LL14 2HN | LL142HN | ll14 2hn | ll142hn | Wrexham | Wrecsam | Froncysyllte STW | 4691 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329500 | 345995 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HP | LL142HP | ll14 2hp | ll142hp | Wrexham | Wrecsam | Froncysyllte STW | 4688 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329754 | 345829 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HR | LL142HR | ll14 2hr | ll142hr | Wrexham | Wrecsam | Froncysyllte STW | 4757 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329722 | 345934 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HS | LL142HS | ll14 2hs | ll142hs | Wrexham | Wrecsam | Froncysyllte STW | 4437 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329484 | 345707 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HT | LL142HT | ll14 2ht | ll142ht | Wrexham | Wrecsam | Froncysyllte STW | 4462 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329059 | 345972 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HU | LL142HU | ll14 2hu | ll142hu | Wrexham | Wrecsam | Froncysyllte STW | 4645 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329065 | 346172 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HW | LL142HW | ll14 2hw | ll142hw | Wrexham | Wrecsam | Froncysyllte STW | 4789 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329489 | 346115 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HY | LL142HY | ll14 2hy | ll142hy | Wrexham | Wrecsam | Froncysyllte STW | 4769 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329138 | 346275 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LA | LL142LA | ll14 2la | ll142la | Wrexham | Wrecsam | Froncysyllte STW | 4816 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329095 | 346346 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LB | LL142LB | ll14 2lb | ll142lb | Wrexham | Wrecsam | Froncysyllte STW | 4738 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329134 | 346242 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LD | LL142LD | ll14 2ld | ll142ld | Wrexham | Wrecsam | Froncysyllte STW | 4945 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329088 | 346490 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LE | LL142LE | ll14 2le | ll142le | Wrexham | Wrecsam | Froncysyllte STW | 4979 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329035 | 346550 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LF | LL142LF | ll14 2lf | ll142lf | Wrexham | Wrecsam | Froncysyllte STW | 5037 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329024 | 346617 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LG | LL142LG | ll14 2lg | ll142lg | Wrexham | Wrecsam | Froncysyllte STW | 5115 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328957 | 346728 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LH | LL142LH | ll14 2lh | ll142lh | Wrexham | Wrecsam | Froncysyllte STW | 5074 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329007 | 346664 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LL | LL142LL | ll14 2ll | ll142ll | Wrexham | Wrecsam | Froncysyllte STW | 4971 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329072 | 346526 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LN | LL142LN | ll14 2ln | ll142ln | Wrexham | Wrecsam | Froncysyllte STW | 5163 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328999 | 346763 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LP | LL142LP | ll14 2lp | ll142lp | Wrexham | Wrecsam | Froncysyllte STW | 5351 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328874 | 347010 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LR | LL142LR | ll14 2lr | ll142lr | Wrexham | Wrecsam | Froncysyllte STW | 5285 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328883 | 346937 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LS | LL142LS | ll14 2ls | ll142ls | Wrexham | Wrecsam | Froncysyllte STW | 5383 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328864 | 347047 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LT | LL142LT | ll14 2lt | ll142lt | Wrexham | Wrecsam | Froncysyllte STW | 5398 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328902 | 347050 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LW | LL142LW | ll14 2lw | ll142lw | Wrexham | Wrecsam | Froncysyllte STW | 5262 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328956 | 346886 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2LY | LL142LY | ll14 2ly | ll142ly | Wrexham | Wrecsam | Froncysyllte STW | 3464 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 327995 | 345308 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NA | LL142NA | ll14 2na | ll142na | Wrexham | Wrecsam | Froncysyllte STW | 4001 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328938 | 345517 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NB | LL142NB | ll14 2nb | ll142nb | Wrexham | Wrecsam | Froncysyllte STW | 3983 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 329043 | 345441 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2ND | LL142ND | ll14 2nd | ll142nd | Wrexham | Wrecsam | Froncysyllte STW | 4004 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 329076 | 345447 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NE | LL142NE | ll14 2ne | ll142ne | Wrexham | Wrecsam | Froncysyllte STW | 3926 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 329206 | 345278 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NF | LL142NF | ll14 2nf | ll142nf | Wrexham | Wrecsam | Froncysyllte STW | 3817 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 329104 | 345213 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NG | LL142NG | ll14 2ng | ll142ng | Wrexham | Wrecsam | Froncysyllte STW | 3811 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328915 | 345315 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NH | LL142NH | ll14 2nh | ll142nh | Wrexham | Wrecsam | Froncysyllte STW | 3828 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328847 | 345370 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NL | LL142NL | ll14 2nl | ll142nl | Wrexham | Wrecsam | Froncysyllte STW | 3957 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328842 | 345516 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NN | LL142NN | ll14 2nn | ll142nn | Wrexham | Wrecsam | Froncysyllte STW | 3916 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328838 | 345473 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NP | LL142NP | ll14 2np | ll142np | Wrexham | Wrecsam | Froncysyllte STW | 3984 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328985 | 345474 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NR | LL142NR | ll14 2nr | ll142nr | Wrexham | Wrecsam | Froncysyllte STW | 3930 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 329018 | 345394 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NS | LL142NS | ll14 2ns | ll142ns | Wrexham | Wrecsam | Froncysyllte STW | 3906 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 329052 | 345347 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NT | LL142NT | ll14 2nt | ll142nt | Wrexham | Wrecsam | Froncysyllte STW | 3893 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 329151 | 345274 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NU | LL142NU | ll14 2nu | ll142nu | Wrexham | Wrecsam | Froncysyllte STW | 3827 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 329213 | 345156 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2NW | LL142NW | ll14 2nw | ll142nw | Wrexham | Wrecsam | Froncysyllte STW | 3921 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328913 | 345440 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PA | LL142PA | ll14 2pa | ll142pa | Wrexham | Wrecsam | Froncysyllte STW | 3851 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328944 | 345345 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PB | LL142PB | ll14 2pb | ll142pb | Wrexham | Wrecsam | Froncysyllte STW | 3833 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328878 | 345360 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PD | LL142PD | ll14 2pd | ll142pd | Wrexham | Wrecsam | Froncysyllte STW | 3756 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328808 | 345309 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PE | LL142PE | ll14 2pe | ll142pe | Wrexham | Wrecsam | Froncysyllte STW | 3748 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328768 | 345320 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PF | LL142PF | ll14 2pf | ll142pf | Wrexham | Wrecsam | Froncysyllte STW | 3698 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328820 | 345237 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PG | LL142PG | ll14 2pg | ll142pg | Wrexham | Wrecsam | Froncysyllte STW | 3641 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328491 | 345328 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PH | LL142PH | ll14 2ph | ll142ph | Wrexham | Wrecsam | Froncysyllte STW | 3867 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328640 | 345510 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PJ | LL142PJ | ll14 2pj | ll142pj | Wrexham | Wrecsam | Froncysyllte STW | 3759 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328683 | 345373 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PL | LL142PL | ll14 2pl | ll142pl | Wrexham | Wrecsam | Froncysyllte STW | 3848 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328596 | 345508 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PN | LL142PN | ll14 2pn | ll142pn | Wrexham | Wrecsam | Froncysyllte STW | 4036 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328751 | 345646 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PP | LL142PP | ll14 2pp | ll142pp | Wrexham | Wrecsam | Froncysyllte STW | 4569 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 328154 | 346407 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PQ | LL142PQ | ll14 2pq | ll142pq | Wrexham | Wrecsam | Froncysyllte STW | 3907 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328779 | 345491 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PR | LL142PR | ll14 2pr | ll142pr | Wrexham | Wrecsam | Froncysyllte STW | 3658 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328378 | 345390 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PS | LL142PS | ll14 2ps | ll142ps | Wrexham | Wrecsam | Froncysyllte STW | 3802 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 328484 | 345504 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PT | LL142PT | ll14 2pt | ll142pt | Wrexham | Wrecsam | Froncysyllte STW | 3735 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328337 | 345486 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PU | LL142PU | ll14 2pu | ll142pu | Wrexham | Wrecsam | Froncysyllte STW | 3594 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328054 | 345427 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PW | LL142PW | ll14 2pw | ll142pw | Wrexham | Wrecsam | Froncysyllte STW | 3881 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 328489 | 345586 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2PY | LL142PY | ll14 2py | ll142py | Wrexham | Wrecsam | Froncysyllte STW | 3639 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328194 | 345433 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RA | LL142RA | ll14 2ra | ll142ra | Wrexham | Wrecsam | Froncysyllte STW | 3636 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328035 | 345475 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RB | LL142RB | ll14 2rb | ll142rb | Wrexham | Wrecsam | Froncysyllte STW | 3600 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328006 | 345445 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RD | LL142RD | ll14 2rd | ll142rd | Wrexham | Wrecsam | Froncysyllte STW | 3476 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328042 | 345307 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RE | LL142RE | ll14 2re | ll142re | Wrexham | Wrecsam | Froncysyllte STW | 3483 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 327943 | 345341 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RF | LL142RF | ll14 2rf | ll142rf | Wrexham | Wrecsam | Froncysyllte STW | 3400 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 327920 | 345261 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RG | LL142RG | ll14 2rg | ll142rg | Wrexham | Wrecsam | Froncysyllte STW | 3375 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 327870 | 345247 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RH | LL142RH | ll14 2rh | ll142rh | Wrexham | Wrecsam | Froncysyllte STW | 3468 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 327654 | 345384 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RL | LL142RL | ll14 2rl | ll142rl | Wrexham | Wrecsam | Froncysyllte STW | 3351 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 327602 | 345274 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RN | LL142RN | ll14 2rn | ll142rn | Wrexham | Wrecsam | Froncysyllte STW | 3420 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328260 | 345180 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RP | LL142RP | ll14 2rp | ll142rp | Wrexham | Wrecsam | Froncysyllte STW | 3361 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328017 | 345195 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RR | LL142RR | ll14 2rr | ll142rr | Wrexham | Wrecsam | Froncysyllte STW | 3377 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328248 | 345138 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RS | LL142RS | ll14 2rs | ll142rs | Wrexham | Wrecsam | Froncysyllte STW | 3351 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328284 | 345097 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RT | LL142RT | ll14 2rt | ll142rt | Wrexham | Wrecsam | Froncysyllte STW | 3425 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328112 | 345234 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RU | LL142RU | ll14 2ru | ll142ru | Wrexham | Wrecsam | Froncysyllte STW | 3452 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328246 | 345218 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RW | LL142RW | ll14 2rw | ll142rw | Wrexham | Wrecsam | Froncysyllte STW | 3488 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328285 | 345243 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2RY | LL142RY | ll14 2ry | ll142ry | Wrexham | Wrecsam | Froncysyllte STW | 3450 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328379 | 345167 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SA | LL142SA | ll14 2sa | ll142sa | Wrexham | Wrecsam | Froncysyllte STW | 3478 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328726 | 345039 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SD | LL142SD | ll14 2sd | ll142sd | Wrexham | Wrecsam | Froncysyllte STW | 3439 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328592 | 345062 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SE | LL142SE | ll14 2se | ll142se | Wrexham | Wrecsam | Froncysyllte STW | 3938 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 328463 | 345657 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SF | LL142SF | ll14 2sf | ll142sf | Wrexham | Wrecsam | Froncysyllte STW | 3868 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328725 | 345473 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SG | LL142SG | ll14 2sg | ll142sg | Wrexham | Wrecsam | Froncysyllte STW | 3484 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328131 | 345290 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SH | LL142SH | ll14 2sh | ll142sh | Wrexham | Wrecsam | Froncysyllte STW | 5184 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330106 | 346188 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SJ | LL142SJ | ll14 2sj | ll142sj | Wrexham | Wrecsam | Froncysyllte STW | 3562 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328662 | 345165 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SL | LL142SL | ll14 2sl | ll142sl | Wrexham | Wrecsam | Froncysyllte STW | 5205 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330084 | 346229 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SN | LL142SN | ll14 2sn | ll142sn | Wrexham | Wrecsam | Froncysyllte STW | 5286 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330085 | 346327 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SP | LL142SP | ll14 2sp | ll142sp | Wrexham | Wrecsam | Froncysyllte STW | 5220 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330416 | 345997 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SR | LL142SR | ll14 2sr | ll142sr | Wrexham | Wrecsam | Froncysyllte STW | 5239 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330361 | 346066 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SS | LL142SS | ll14 2ss | ll142ss | Wrexham | Wrecsam | Cefn Mawr WwTW | 5315 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330573 | 345998 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2ST | LL142ST | ll14 2st | ll142st | Wrexham | Wrecsam | Froncysyllte STW | 5239 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330236 | 346162 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SU | LL142SU | ll14 2su | ll142su | Wrexham | Wrecsam | Froncysyllte STW | 5296 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330384 | 346121 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SW | LL142SW | ll14 2sw | ll142sw | Wrexham | Wrecsam | Froncysyllte STW | 5167 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330185 | 346110 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SX | LL142SX | ll14 2sx | ll142sx | Wrexham | Wrecsam | Froncysyllte STW | 5281 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330187 | 346250 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2SY | LL142SY | ll14 2sy | ll142sy | Wrexham | Wrecsam | Froncysyllte STW | 5120 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330185 | 346051 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TA | LL142TA | ll14 2ta | ll142ta | Wrexham | Wrecsam | Froncysyllte STW | 5164 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330263 | 346048 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TB | LL142TB | ll14 2tb | ll142tb | Wrexham | Wrecsam | Froncysyllte STW | 5358 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330366 | 346213 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TD | LL142TD | ll14 2td | ll142td | Wrexham | Wrecsam | Froncysyllte STW | 5451 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330585 | 346157 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TE | LL142TE | ll14 2te | ll142te | Wrexham | Wrecsam | Froncysyllte STW | 5340 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330462 | 346114 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TF | LL142TF | ll14 2tf | ll142tf | Wrexham | Wrecsam | Froncysyllte STW | 5329 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330501 | 346069 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TG | LL142TG | ll14 2tg | ll142tg | Wrexham | Wrecsam | Cefn Mawr WwTW | 5350 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330563 | 346049 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TH | LL142TH | ll14 2th | ll142th | Wrexham | Wrecsam | Cefn Mawr WwTW | 5367 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330617 | 346031 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TL | LL142TL | ll14 2tl | ll142tl | Wrexham | Wrecsam | Cefn Mawr WwTW | 5216 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330565 | 345881 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TN | LL142TN | ll14 2tn | ll142tn | Wrexham | Wrecsam | Cefn Mawr WwTW | 5214 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330597 | 345855 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TP | LL142TP | ll14 2tp | ll142tp | Wrexham | Wrecsam | Cefn Mawr WwTW | 5191 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330522 | 345882 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TR | LL142TR | ll14 2tr | ll142tr | Wrexham | Wrecsam | Froncysyllte STW | 3431 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328451 | 345117 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TS | LL142TS | ll14 2ts | ll142ts | Wrexham | Wrecsam | Froncysyllte STW | 5584 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330667 | 346262 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2TW | LL142TW | ll14 2tw | ll142tw | Wrexham | Wrecsam | Cefn Mawr WwTW | 5096 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330534 | 345755 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AA | LL143AA | ll14 3aa | ll143aa | Wrexham | Wrecsam | Cefn Mawr WwTW | 752 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327829 | 342349 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AB | LL143AB | ll14 3ab | ll143ab | Wrexham | Wrecsam | Cefn Mawr WwTW | 721 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327933 | 342235 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AE | LL143AE | ll14 3ae | ll143ae | Wrexham | Wrecsam | Cefn Mawr WwTW | 856 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328077 | 342283 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AF | LL143AF | ll14 3af | ll143af | Wrexham | Wrecsam | Cefn Mawr WwTW | 949 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328129 | 342362 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AH | LL143AH | ll14 3ah | ll143ah | Wrexham | Wrecsam | Cefn Mawr WwTW | 923 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328086 | 342368 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AJ | LL143AJ | ll14 3aj | ll143aj | Wrexham | Wrecsam | Cefn Mawr WwTW | 921 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328340 | 341937 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AL | LL143AL | ll14 3al | ll143al | Wrexham | Wrecsam | Cefn Mawr WwTW | 942 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328103 | 342378 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AN | LL143AN | ll14 3an | ll143an | Wrexham | Wrecsam | Cefn Mawr WwTW | 1022 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328168 | 342427 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AQ | LL143AQ | ll14 3aq | ll143aq | Wrexham | Wrecsam | Cefn Mawr WwTW | 946 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328337 | 342027 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AR | LL143AR | ll14 3ar | ll143ar | Wrexham | Wrecsam | Cefn Mawr WwTW | 940 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328041 | 342431 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AS | LL143AS | ll14 3as | ll143as | Wrexham | Wrecsam | Cefn Mawr WwTW | 896 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328121 | 342294 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AT | LL143AT | ll14 3at | ll143at | Wrexham | Wrecsam | Cefn Mawr WwTW | 719 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328038 | 342114 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AU | LL143AU | ll14 3au | ll143au | Wrexham | Wrecsam | Cefn Mawr WwTW | 2170 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328700 | 343473 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AW | LL143AW | ll14 3aw | ll143aw | Wrexham | Wrecsam | Cefn Mawr WwTW | 963 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328094 | 342416 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AX | LL143AX | ll14 3ax | ll143ax | Wrexham | Wrecsam | Cefn Mawr WwTW | 1025 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328342 | 342205 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AY | LL143AY | ll14 3ay | ll143ay | Wrexham | Wrecsam | Cefn Mawr WwTW | 709 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327976 | 342175 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3AZ | LL143AZ | ll14 3az | ll143az | Wrexham | Wrecsam | Froncysyllte STW | 1239 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327775 | 343005 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BA | LL143BA | ll14 3ba | ll143ba | Wrexham | Wrecsam | Cefn Mawr WwTW | 660 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327883 | 342198 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BB | LL143BB | ll14 3bb | ll143bb | Wrexham | Wrecsam | Cefn Mawr WwTW | 644 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327913 | 342147 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BD | LL143BD | ll14 3bd | ll143bd | Wrexham | Wrecsam | Cefn Mawr WwTW | 616 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327769 | 342227 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BE | LL143BE | ll14 3be | ll143be | Wrexham | Wrecsam | Cefn Mawr WwTW | 586 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327748 | 342204 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BF | LL143BF | ll14 3bf | ll143bf | Wrexham | Wrecsam | Cefn Mawr WwTW | 972 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328217 | 342296 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BG | LL143BG | ll14 3bg | ll143bg | Wrexham | Wrecsam | Cefn Mawr WwTW | 579 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327762 | 342188 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BH | LL143BH | ll14 3bh | ll143bh | Wrexham | Wrecsam | Cefn Mawr WwTW | 857 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327862 | 342451 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BJ | LL143BJ | ll14 3bj | ll143bj | Wrexham | Wrecsam | Cefn Mawr WwTW | 925 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328365 | 341835 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BL | LL143BL | ll14 3bl | ll143bl | Wrexham | Wrecsam | Cefn Mawr WwTW | 971 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327897 | 342562 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BN | LL143BN | ll14 3bn | ll143bn | Wrexham | Wrecsam | Cefn Mawr WwTW | 890 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327896 | 342470 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BP | LL143BP | ll14 3bp | ll143bp | Wrexham | Wrecsam | Froncysyllte STW | 1135 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327928 | 342747 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BQ | LL143BQ | ll14 3bq | ll143bq | Wrexham | Wrecsam | Cefn Mawr WwTW | 603 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327835 | 342164 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BS | LL143BS | ll14 3bs | ll143bs | Wrexham | Wrecsam | Froncysyllte STW | 1130 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327931 | 342736 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BT | LL143BT | ll14 3bt | ll143bt | Wrexham | Wrecsam | Froncysyllte STW | 1113 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327930 | 342712 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BU | LL143BU | ll14 3bu | ll143bu | Wrexham | Wrecsam | Froncysyllte STW | 1087 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327926 | 342677 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BW | LL143BW | ll14 3bw | ll143bw | Wrexham | Wrecsam | Cefn Mawr WwTW | 1055 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327920 | 342644 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BX | LL143BX | ll14 3bx | ll143bx | Wrexham | Wrecsam | Cefn Mawr WwTW | 1369 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328505 | 342571 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BY | LL143BY | ll14 3by | ll143by | Wrexham | Wrecsam | Cefn Mawr WwTW | 738 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327913 | 342275 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3BZ | LL143BZ | ll14 3bz | ll143bz | Wrexham | Wrecsam | Cefn Mawr WwTW | 564 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327786 | 342153 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DA | LL143DA | ll14 3da | ll143da | Wrexham | Wrecsam | Cefn Mawr WwTW | 745 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327938 | 342262 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DD | LL143DD | ll14 3dd | ll143dd | Wrexham | Wrecsam | Cefn Mawr WwTW | 818 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327979 | 342324 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DE | LL143DE | ll14 3de | ll143de | Wrexham | Wrecsam | Cefn Mawr WwTW | 874 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327967 | 342404 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DF | LL143DF | ll14 3df | ll143df | Wrexham | Wrecsam | Cefn Mawr WwTW | 927 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327988 | 342455 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DG | LL143DG | ll14 3dg | ll143dg | Wrexham | Wrecsam | Cefn Mawr WwTW | 1003 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327982 | 342550 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DH | LL143DH | ll14 3dh | ll143dh | Wrexham | Wrecsam | Cefn Mawr WwTW | 990 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328002 | 342522 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DJ | LL143DJ | ll14 3dj | ll143dj | Wrexham | Wrecsam | Cefn Mawr WwTW | 947 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328395 | 341756 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DL | LL143DL | ll14 3dl | ll143dl | Wrexham | Wrecsam | Cefn Mawr WwTW | 1300 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328125 | 342811 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DN | LL143DN | ll14 3dn | ll143dn | Wrexham | Wrecsam | Cefn Mawr WwTW | 1157 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328024 | 342704 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DP | LL143DP | ll14 3dp | ll143dp | Wrexham | Wrecsam | Cefn Mawr WwTW | 1200 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328031 | 342750 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DR | LL143DR | ll14 3dr | ll143dr | Wrexham | Wrecsam | Froncysyllte STW | 1185 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327983 | 342761 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DS | LL143DS | ll14 3ds | ll143ds | Wrexham | Wrecsam | Cefn Mawr WwTW | 1088 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328035 | 342617 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DT | LL143DT | ll14 3dt | ll143dt | Wrexham | Wrecsam | Cefn Mawr WwTW | 743 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328046 | 342144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DW | LL143DW | ll14 3dw | ll143dw | Wrexham | Wrecsam | Cefn Mawr WwTW | 1131 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327955 | 342712 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DX | LL143DX | ll14 3dx | ll143dx | Wrexham | Wrecsam | Cefn Mawr WwTW | 1417 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328418 | 342734 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3DZ | LL143DZ | ll14 3dz | ll143dz | Wrexham | Wrecsam | Cefn Mawr WwTW | 1505 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328584 | 342688 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EA | LL143EA | ll14 3ea | ll143ea | Wrexham | Wrecsam | Cefn Mawr WwTW | 1400 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328436 | 342693 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EB | LL143EB | ll14 3eb | ll143eb | Wrexham | Wrecsam | Cefn Mawr WwTW | 1376 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328378 | 342715 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EE | LL143EE | ll14 3ee | ll143ee | Wrexham | Wrecsam | Cefn Mawr WwTW | 1534 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328586 | 342730 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EF | LL143EF | ll14 3ef | ll143ef | Wrexham | Wrecsam | Cefn Mawr WwTW | 1408 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328535 | 342597 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EG | LL143EG | ll14 3eg | ll143eg | Wrexham | Wrecsam | Cefn Mawr WwTW | 1872 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328853 | 342938 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EH | LL143EH | ll14 3eh | ll143eh | Wrexham | Wrecsam | Cefn Mawr WwTW | 2427 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 329400 | 343144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EJ | LL143EJ | ll14 3ej | ll143ej | Wrexham | Wrecsam | Cefn Mawr WwTW | 971 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328421 | 341697 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EN | LL143EN | ll14 3en | ll143en | Wrexham | Wrecsam | Cefn Mawr WwTW | 1584 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328625 | 342762 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EP | LL143EP | ll14 3ep | ll143ep | Wrexham | Wrecsam | Cefn Mawr WwTW | 2259 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 329053 | 343291 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EQ | LL143EQ | ll14 3eq | ll143eq | Wrexham | Wrecsam | Cefn Mawr WwTW | 1405 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328485 | 342649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3ER | LL143ER | ll14 3er | ll143er | Wrexham | Wrecsam | Cefn Mawr WwTW | 2211 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328989 | 343287 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3ES | LL143ES | ll14 3es | ll143es | Wrexham | Wrecsam | Cefn Mawr WwTW | 2302 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 329088 | 343317 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3ET | LL143ET | ll14 3et | ll143et | Wrexham | Wrecsam | Cefn Mawr WwTW | 2347 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 329089 | 343379 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EU | LL143EU | ll14 3eu | ll143eu | Wrexham | Wrecsam | Cefn Mawr WwTW | 2306 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 329013 | 343395 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EW | LL143EW | ll14 3ew | ll143ew | Wrexham | Wrecsam | Cefn Mawr WwTW | 1722 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328726 | 342855 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EX | LL143EX | ll14 3ex | ll143ex | Wrexham | Wrecsam | Cefn Mawr WwTW | 1465 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328541 | 342677 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EY | LL143EY | ll14 3ey | ll143ey | Wrexham | Wrecsam | Cefn Mawr WwTW | 2362 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 329025 | 343459 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3EZ | LL143EZ | ll14 3ez | ll143ez | Wrexham | Wrecsam | Cefn Mawr WwTW | 1508 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328553 | 342727 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3GB | LL143GB | ll14 3gb | ll143gb | Wrexham | Wrecsam | Froncysyllte STW | 1280 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327823 | 343022 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HA | LL143HA | ll14 3ha | ll143ha | Wrexham | Wrecsam | Cefn Mawr WwTW | 2412 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 329044 | 343509 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HB | LL143HB | ll14 3hb | ll143hb | Wrexham | Wrecsam | Cefn Mawr WwTW | 2452 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 329028 | 343576 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HD | LL143HD | ll14 3hd | ll143hd | Wrexham | Wrecsam | Cefn Mawr WwTW | 2356 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 328931 | 343531 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HE | LL143HE | ll14 3he | ll143he | Wrexham | Wrecsam | Cefn Mawr WwTW | 2290 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 328845 | 343515 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HF | LL143HF | ll14 3hf | ll143hf | Wrexham | Wrecsam | Cefn Mawr WwTW | 2123 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328916 | 343235 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HG | LL143HG | ll14 3hg | ll143hg | Wrexham | Wrecsam | Cefn Mawr WwTW | 2106 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328874 | 343251 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HL | LL143HL | ll14 3hl | ll143hl | Wrexham | Wrecsam | Cefn Mawr WwTW | 2159 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328750 | 343423 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HN | LL143HN | ll14 3hn | ll143hn | Wrexham | Wrecsam | Froncysyllte STW | 1783 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328253 | 343328 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HP | LL143HP | ll14 3hp | ll143hp | Wrexham | Wrecsam | Froncysyllte STW | 1681 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328237 | 343206 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HQ | LL143HQ | ll14 3hq | ll143hq | Wrexham | Wrecsam | Froncysyllte STW | 1754 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328269 | 343276 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HR | LL143HR | ll14 3hr | ll143hr | Wrexham | Wrecsam | Froncysyllte STW | 1838 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328312 | 343350 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HS | LL143HS | ll14 3hs | ll143hs | Wrexham | Wrecsam | Froncysyllte STW | 1826 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328350 | 343300 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HT | LL143HT | ll14 3ht | ll143ht | Wrexham | Wrecsam | Froncysyllte STW | 1902 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328410 | 343347 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HU | LL143HU | ll14 3hu | ll143hu | Wrexham | Wrecsam | Froncysyllte STW | 1975 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328455 | 343405 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3HY | LL143HY | ll14 3hy | ll143hy | Wrexham | Wrecsam | Cefn Mawr WwTW | 2043 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328545 | 343424 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3JA | LL143JA | ll14 3ja | ll143ja | Wrexham | Wrecsam | Cefn Mawr WwTW | 1040 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328478 | 341542 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3JD | LL143JD | ll14 3jd | ll143jd | Wrexham | Wrecsam | Cefn Mawr WwTW | 1221 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 328670 | 341738 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3JE | LL143JE | ll14 3je | ll143je | Wrexham | Wrecsam | Cefn Mawr WwTW | 1407 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 328854 | 341787 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3JF | LL143JF | ll14 3jf | ll143jf | Wrexham | Wrecsam | Cefn Mawr WwTW | 1288 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 328735 | 341625 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3JG | LL143JG | ll14 3jg | ll143jg | Wrexham | Wrecsam | Cefn Mawr WwTW | 954 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 328372 | 341458 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3JH | LL143JH | ll14 3jh | ll143jh | Wrexham | Wrecsam | Cefn Mawr WwTW | 1101 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 328539 | 341542 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3JJ | LL143JJ | ll14 3jj | ll143jj | Wrexham | Wrecsam | Cefn Mawr WwTW | 1110 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 328554 | 341591 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3JL | LL143JL | ll14 3jl | ll143jl | Wrexham | Wrecsam | Cefn Mawr WwTW | 1096 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 328544 | 341646 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3JN | LL143JN | ll14 3jn | ll143jn | Wrexham | Wrecsam | Cefn Mawr WwTW | 1088 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 328533 | 341600 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3JQ | LL143JQ | ll14 3jq | ll143jq | Wrexham | Wrecsam | Cefn Mawr WwTW | 1153 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 328600 | 341628 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3JW | LL143JW | ll14 3jw | ll143jw | Wrexham | Wrecsam | Cefn Mawr WwTW | 1062 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 328510 | 341640 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LA | LL143LA | ll14 3la | ll143la | Wrexham | Wrecsam | Cefn Mawr WwTW | 2060 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328532 | 343452 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LB | LL143LB | ll14 3lb | ll143lb | Wrexham | Wrecsam | Cefn Mawr WwTW | 1905 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328455 | 343317 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LD | LL143LD | ll14 3ld | ll143ld | Wrexham | Wrecsam | Cefn Mawr WwTW | 1986 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328535 | 343363 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LE | LL143LE | ll14 3le | ll143le | Wrexham | Wrecsam | Cefn Mawr WwTW | 2103 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328778 | 343330 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LF | LL143LF | ll14 3lf | ll143lf | Wrexham | Wrecsam | Cefn Mawr WwTW | 2069 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328686 | 343358 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LG | LL143LG | ll14 3lg | ll143lg | Wrexham | Wrecsam | Cefn Mawr WwTW | 1990 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328747 | 343208 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LH | LL143LH | ll14 3lh | ll143lh | Wrexham | Wrecsam | Froncysyllte STW | 1932 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328317 | 343468 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LJ | LL143LJ | ll14 3lj | ll143lj | Wrexham | Wrecsam | Froncysyllte STW | 2034 | 915 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.05 | 9.1 | 10.05 | 328420 | 343515 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LN | LL143LN | ll14 3ln | ll143ln | Wrexham | Wrecsam | Cefn Mawr WwTW | 700 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327833 | 342286 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LP | LL143LP | ll14 3lp | ll143lp | Wrexham | Wrecsam | Cefn Mawr WwTW | 582 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327830 | 342141 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LR | LL143LR | ll14 3lr | ll143lr | Wrexham | Wrecsam | Cefn Mawr WwTW | 487 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327772 | 342065 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LS | LL143LS | ll14 3ls | ll143ls | Wrexham | Wrecsam | Cefn Mawr WwTW | 377 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327759 | 341916 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LT | LL143LT | ll14 3lt | ll143lt | Wrexham | Wrecsam | Cefn Mawr WwTW | 418 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327819 | 341897 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LU | LL143LU | ll14 3lu | ll143lu | Wrexham | Wrecsam | Cefn Mawr WwTW | 549 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327985 | 341579 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LX | LL143LX | ll14 3lx | ll143lx | Wrexham | Wrecsam | Froncysyllte STW | 1983 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328425 | 343444 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3LY | LL143LY | ll14 3ly | ll143ly | Wrexham | Wrecsam | Cefn Mawr WwTW | 571 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328012 | 341598 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NA | LL143NA | ll14 3na | ll143na | Wrexham | Wrecsam | Cefn Mawr WwTW | 555 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328004 | 341671 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NB | LL143NB | ll14 3nb | ll143nb | Wrexham | Wrecsam | Cefn Mawr WwTW | 450 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327900 | 341709 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3ND | LL143ND | ll14 3nd | ll143nd | Wrexham | Wrecsam | Cefn Mawr WwTW | 313 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327728 | 341844 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NE | LL143NE | ll14 3ne | ll143ne | Wrexham | Wrecsam | Cefn Mawr WwTW | 344 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327739 | 341886 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NF | LL143NF | ll14 3nf | ll143nf | Wrexham | Wrecsam | Cefn Mawr WwTW | 338 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327582 | 342011 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NG | LL143NG | ll14 3ng | ll143ng | Wrexham | Wrecsam | Cefn Mawr WwTW | 398 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327848 | 341705 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NH | LL143NH | ll14 3nh | ll143nh | Wrexham | Wrecsam | Cefn Mawr WwTW | 535 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327691 | 342177 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NJ | LL143NJ | ll14 3nj | ll143nj | Wrexham | Wrecsam | Cefn Mawr WwTW | 490 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327703 | 342120 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NL | LL143NL | ll14 3nl | ll143nl | Wrexham | Wrecsam | Froncysyllte STW | 615 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327592 | 342341 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NN | LL143NN | ll14 3nn | ll143nn | Wrexham | Wrecsam | Cefn Mawr WwTW | 624 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327701 | 342271 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NP | LL143NP | ll14 3np | ll143np | Wrexham | Wrecsam | Froncysyllte STW | 594 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327569 | 342337 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NQ | LL143NQ | ll14 3nq | ll143nq | Wrexham | Wrecsam | Cefn Mawr WwTW | 601 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327874 | 342126 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NU | LL143NU | ll14 3nu | ll143nu | Wrexham | Wrecsam | Cefn Mawr WwTW | 530 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327854 | 342043 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NW | LL143NW | ll14 3nw | ll143nw | Wrexham | Wrecsam | Froncysyllte STW | 560 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327528 | 342332 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3NY | LL143NY | ll14 3ny | ll143ny | Wrexham | Wrecsam | Cefn Mawr WwTW | 512 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327923 | 341895 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PA | LL143PA | ll14 3pa | ll143pa | Wrexham | Wrecsam | Cefn Mawr WwTW | 553 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327977 | 341867 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PB | LL143PB | ll14 3pb | ll143pb | Wrexham | Wrecsam | Cefn Mawr WwTW | 469 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327844 | 341954 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PD | LL143PD | ll14 3pd | ll143pd | Wrexham | Wrecsam | Cefn Mawr WwTW | 541 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327986 | 341772 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PE | LL143PE | ll14 3pe | ll143pe | Wrexham | Wrecsam | Cefn Mawr WwTW | 802 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328246 | 341602 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PF | LL143PF | ll14 3pf | ll143pf | Wrexham | Wrecsam | Cefn Mawr WwTW | 497 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327944 | 341754 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PG | LL143PG | ll14 3pg | ll143pg | Wrexham | Wrecsam | Cefn Mawr WwTW | 614 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328063 | 341677 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PH | LL143PH | ll14 3ph | ll143ph | Wrexham | Wrecsam | Cefn Mawr WwTW | 658 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328100 | 341799 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PL | LL143PL | ll14 3pl | ll143pl | Wrexham | Wrecsam | Cefn Mawr WwTW | 757 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328150 | 341988 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PN | LL143PN | ll14 3pn | ll143pn | Wrexham | Wrecsam | Cefn Mawr WwTW | 648 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328097 | 341721 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PP | LL143PP | ll14 3pp | ll143pp | Wrexham | Wrecsam | Cefn Mawr WwTW | 764 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328200 | 341846 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PR | LL143PR | ll14 3pr | ll143pr | Wrexham | Wrecsam | Cefn Mawr WwTW | 825 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328266 | 341820 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PS | LL143PS | ll14 3ps | ll143ps | Wrexham | Wrecsam | Cefn Mawr WwTW | 669 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328093 | 341884 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PT | LL143PT | ll14 3pt | ll143pt | Wrexham | Wrecsam | Cefn Mawr WwTW | 706 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328107 | 341959 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PU | LL143PU | ll14 3pu | ll143pu | Wrexham | Wrecsam | Cefn Mawr WwTW | 774 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328155 | 342020 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PW | LL143PW | ll14 3pw | ll143pw | Wrexham | Wrecsam | Cefn Mawr WwTW | 732 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328162 | 341867 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3PY | LL143PY | ll14 3py | ll143py | Wrexham | Wrecsam | Cefn Mawr WwTW | 625 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328009 | 341978 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3QA | LL143QA | ll14 3qa | ll143qa | Wrexham | Wrecsam | Froncysyllte STW | 1129 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327826 | 342833 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RA | LL143RA | ll14 3ra | ll143ra | Wrexham | Wrecsam | Cefn Mawr WwTW | 694 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 327824 | 342284 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RB | LL143RB | ll14 3rb | ll143rb | Wrexham | Wrecsam | Cefn Mawr WwTW | 758 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328208 | 341686 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RD | LL143RD | ll14 3rd | ll143rd | Wrexham | Wrecsam | Cefn Mawr WwTW | 874 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328319 | 341614 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RE | LL143RE | ll14 3re | ll143re | Wrexham | Wrecsam | Froncysyllte STW | 1160 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327893 | 342816 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RF | LL143RF | ll14 3rf | ll143rf | Wrexham | Wrecsam | Froncysyllte STW | 1174 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327893 | 342834 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RG | LL143RG | ll14 3rg | ll143rg | Wrexham | Wrecsam | Froncysyllte STW | 1084 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327885 | 342718 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RH | LL143RH | ll14 3rh | ll143rh | Wrexham | Wrecsam | Froncysyllte STW | 1262 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327853 | 342979 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RJ | LL143RJ | ll14 3rj | ll143rj | Wrexham | Wrecsam | Froncysyllte STW | 1256 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327923 | 342917 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RL | LL143RL | ll14 3rl | ll143rl | Wrexham | Wrecsam | Froncysyllte STW | 1293 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327863 | 343011 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RN | LL143RN | ll14 3rn | ll143rn | Wrexham | Wrecsam | Froncysyllte STW | 1237 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327929 | 342887 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RP | LL143RP | ll14 3rp | ll143rp | Wrexham | Wrecsam | Froncysyllte STW | 1305 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327803 | 343065 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RR | LL143RR | ll14 3rr | ll143rr | Wrexham | Wrecsam | Froncysyllte STW | 1272 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327769 | 343048 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RS | LL143RS | ll14 3rs | ll143rs | Wrexham | Wrecsam | Froncysyllte STW | 1248 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327745 | 343034 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RT | LL143RT | ll14 3rt | ll143rt | Wrexham | Wrecsam | Froncysyllte STW | 1180 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327668 | 342999 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RU | LL143RU | ll14 3ru | ll143ru | Wrexham | Wrecsam | Froncysyllte STW | 1115 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327588 | 342967 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RW | LL143RW | ll14 3rw | ll143rw | Wrexham | Wrecsam | Froncysyllte STW | 1251 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327902 | 342928 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RX | LL143RX | ll14 3rx | ll143rx | Wrexham | Wrecsam | Froncysyllte STW | 1245 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327876 | 342941 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3RY | LL143RY | ll14 3ry | ll143ry | Wrexham | Wrecsam | Froncysyllte STW | 962 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 327415 | 342872 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SB | LL143SB | ll14 3sb | ll143sb | Wrexham | Wrecsam | Froncysyllte STW | 1201 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327638 | 343038 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SD | LL143SD | ll14 3sd | ll143sd | Wrexham | Wrecsam | Froncysyllte STW | 1254 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327725 | 343052 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SE | LL143SE | ll14 3se | ll143se | Wrexham | Wrecsam | Froncysyllte STW | 1320 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327730 | 343125 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SF | LL143SF | ll14 3sf | ll143sf | Wrexham | Wrecsam | Froncysyllte STW | 1126 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327537 | 343001 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SG | LL143SG | ll14 3sg | ll143sg | Wrexham | Wrecsam | Froncysyllte STW | 891 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 327251 | 342839 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SH | LL143SH | ll14 3sh | ll143sh | Wrexham | Wrecsam | Froncysyllte STW | 1260 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327708 | 343069 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SJ | LL143SJ | ll14 3sj | ll143sj | Wrexham | Wrecsam | Froncysyllte STW | 1362 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327835 | 343112 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SN | LL143SN | ll14 3sn | ll143sn | Wrexham | Wrecsam | Froncysyllte STW | 1037 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327575 | 342886 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SR | LL143SR | ll14 3sr | ll143sr | Wrexham | Wrecsam | Froncysyllte STW | 1104 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 327370 | 343033 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SS | LL143SS | ll14 3ss | ll143ss | Wrexham | Wrecsam | Froncysyllte STW | 1123 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 327332 | 343060 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3ST | LL143ST | ll14 3st | ll143st | Wrexham | Wrecsam | Froncysyllte STW | 940 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 327179 | 342897 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SU | LL143SU | ll14 3su | ll143su | Wrexham | Wrecsam | Froncysyllte STW | 1092 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 326994 | 343045 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SW | LL143SW | ll14 3sw | ll143sw | Wrexham | Wrecsam | Froncysyllte STW | 981 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 327383 | 342902 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SX | LL143SX | ll14 3sx | ll143sx | Wrexham | Wrecsam | Froncysyllte STW | 1157 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 327227 | 343111 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3SY | LL143SY | ll14 3sy | ll143sy | Wrexham | Wrecsam | Froncysyllte STW | 1274 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327953 | 342914 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TA | LL143TA | ll14 3ta | ll143ta | Wrexham | Wrecsam | Froncysyllte STW | 987 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 327279 | 342932 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TB | LL143TB | ll14 3tb | ll143tb | Wrexham | Wrecsam | Froncysyllte STW | 1447 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327795 | 343234 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TD | LL143TD | ll14 3td | ll143td | Wrexham | Wrecsam | Froncysyllte STW | 1440 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327671 | 343286 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TE | LL143TE | ll14 3te | ll143te | Wrexham | Wrecsam | Froncysyllte STW | 1499 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 327401 | 343430 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TF | LL143TF | ll14 3tf | ll143tf | Wrexham | Wrecsam | Froncysyllte STW | 1473 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327702 | 343308 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TG | LL143TG | ll14 3tg | ll143tg | Wrexham | Wrecsam | Froncysyllte STW | 1478 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327603 | 343353 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TH | LL143TH | ll14 3th | ll143th | Wrexham | Wrecsam | Froncysyllte STW | 1494 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327558 | 343385 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TJ | LL143TJ | ll14 3tj | ll143tj | Wrexham | Wrecsam | Froncysyllte STW | 1394 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327583 | 343271 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TL | LL143TL | ll14 3tl | ll143tl | Wrexham | Wrecsam | Froncysyllte STW | 1499 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327540 | 343395 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TN | LL143TN | ll14 3tn | ll143tn | Wrexham | Wrecsam | Froncysyllte STW | 1776 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 327366 | 343717 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TP | LL143TP | ll14 3tp | ll143tp | Wrexham | Wrecsam | Froncysyllte STW | 1435 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327702 | 343267 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TR | LL143TR | ll14 3tr | ll143tr | Wrexham | Wrecsam | Froncysyllte STW | 1538 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327827 | 343320 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TS | LL143TS | ll14 3ts | ll143ts | Wrexham | Wrecsam | Froncysyllte STW | 1774 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328204 | 343356 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TT | LL143TT | ll14 3tt | ll143tt | Wrexham | Wrecsam | Froncysyllte STW | 1603 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327855 | 343379 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TU | LL143TU | ll14 3tu | ll143tu | Wrexham | Wrecsam | Froncysyllte STW | 1671 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327947 | 343406 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TW | LL143TW | ll14 3tw | ll143tw | Wrexham | Wrecsam | Froncysyllte STW | 1563 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327752 | 343384 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TX | LL143TX | ll14 3tx | ll143tx | Wrexham | Wrecsam | Froncysyllte STW | 1442 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327587 | 343320 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TY | LL143TY | ll14 3ty | ll143ty | Wrexham | Wrecsam | Froncysyllte STW | 1690 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327979 | 343409 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3TZ | LL143TZ | ll14 3tz | ll143tz | Wrexham | Wrecsam | Froncysyllte STW | 1372 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327658 | 343217 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UA | LL143UA | ll14 3ua | ll143ua | Wrexham | Wrecsam | Froncysyllte STW | 1733 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328113 | 343373 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UB | LL143UB | ll14 3ub | ll143ub | Wrexham | Wrecsam | Froncysyllte STW | 1813 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328205 | 343404 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UD | LL143UD | ll14 3ud | ll143ud | Wrexham | Wrecsam | Froncysyllte STW | 1827 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328242 | 343393 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UE | LL143UE | ll14 3ue | ll143ue | Wrexham | Wrecsam | Froncysyllte STW | 1648 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328061 | 343305 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UF | LL143UF | ll14 3uf | ll143uf | Wrexham | Wrecsam | Froncysyllte STW | 1795 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328238 | 343356 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UG | LL143UG | ll14 3ug | ll143ug | Wrexham | Wrecsam | Froncysyllte STW | 1872 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328323 | 343385 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UH | LL143UH | ll14 3uh | ll143uh | Wrexham | Wrecsam | Cefn Mawr WwTW | 1913 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328561 | 343257 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UJ | LL143UJ | ll14 3uj | ll143uj | Wrexham | Wrecsam | Froncysyllte STW | 1701 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328124 | 343325 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UL | LL143UL | ll14 3ul | ll143ul | Wrexham | Wrecsam | Cefn Mawr WwTW | 1921 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328604 | 343235 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UN | LL143UN | ll14 3un | ll143un | Wrexham | Wrecsam | Cefn Mawr WwTW | 1716 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328514 | 343046 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UP | LL143UP | ll14 3up | ll143up | Wrexham | Wrecsam | Cefn Mawr WwTW | 1870 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328686 | 343103 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UQ | LL143UQ | ll14 3uq | ll143uq | Wrexham | Wrecsam | Cefn Mawr WwTW | 1629 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328460 | 342977 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UR | LL143UR | ll14 3ur | ll143ur | Wrexham | Wrecsam | Cefn Mawr WwTW | 2083 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328933 | 343162 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3US | LL143US | ll14 3us | ll143us | Wrexham | Wrecsam | Cefn Mawr WwTW | 1887 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328662 | 343145 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UT | LL143UT | ll14 3ut | ll143ut | Wrexham | Wrecsam | Cefn Mawr WwTW | 1966 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328644 | 343261 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UU | LL143UU | ll14 3uu | ll143uu | Wrexham | Wrecsam | Cefn Mawr WwTW | 1954 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328710 | 343193 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UW | LL143UW | ll14 3uw | ll143uw | Wrexham | Wrecsam | Cefn Mawr WwTW | 1766 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328554 | 343078 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3UY | LL143UY | ll14 3uy | ll143uy | Wrexham | Wrecsam | Cefn Mawr WwTW | 1941 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 328652 | 343223 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YA | LL143YA | ll14 3ya | ll143ya | Wrexham | Wrecsam | Froncysyllte STW | 1800 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328141 | 343435 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YB | LL143YB | ll14 3yb | ll143yb | Wrexham | Wrecsam | Froncysyllte STW | 1733 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328050 | 343415 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YD | LL143YD | ll14 3yd | ll143yd | Wrexham | Wrecsam | Cefn Mawr WwTW | 1116 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328237 | 342491 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YE | LL143YE | ll14 3ye | ll143ye | Wrexham | Wrecsam | Cefn Mawr WwTW | 1286 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328420 | 342543 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YF | LL143YF | ll14 3yf | ll143yf | Wrexham | Wrecsam | Cefn Mawr WwTW | 1339 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328332 | 342707 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YG | LL143YG | ll14 3yg | ll143yg | Wrexham | Wrecsam | Cefn Mawr WwTW | 1289 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328344 | 342628 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YH | LL143YH | ll14 3yh | ll143yh | Wrexham | Wrecsam | Cefn Mawr WwTW | 1200 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328260 | 342585 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YJ | LL143YJ | ll14 3yj | ll143yj | Wrexham | Wrecsam | Cefn Mawr WwTW | 1258 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328321 | 342607 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YL | LL143YL | ll14 3yl | ll143yl | Wrexham | Wrecsam | Cefn Mawr WwTW | 1341 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328380 | 342665 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YN | LL143YN | ll14 3yn | ll143yn | Wrexham | Wrecsam | Cefn Mawr WwTW | 1355 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328457 | 342606 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YP | LL143YP | ll14 3yp | ll143yp | Wrexham | Wrecsam | Cefn Mawr WwTW | 1302 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328469 | 342510 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YQ | LL143YQ | ll14 3yq | ll143yq | Wrexham | Wrecsam | Cefn Mawr WwTW | 1312 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328343 | 342660 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YR | LL143YR | ll14 3yr | ll143yr | Wrexham | Wrecsam | Cefn Mawr WwTW | 1130 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328343 | 342392 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YS | LL143YS | ll14 3ys | ll143ys | Wrexham | Wrecsam | Cefn Mawr WwTW | 956 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328390 | 341873 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YT | LL143YT | ll14 3yt | ll143yt | Wrexham | Wrecsam | Cefn Mawr WwTW | 956 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328398 | 341822 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YU | LL143YU | ll14 3yu | ll143yu | Wrexham | Wrecsam | Cefn Mawr WwTW | 1227 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 328399 | 342477 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YW | LL143YW | ll14 3yw | ll143yw | Wrexham | Wrecsam | Cefn Mawr WwTW | 1362 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328414 | 342661 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 3YY | LL143YY | ll14 3yy | ll143yy | Wrexham | Wrecsam | Cefn Mawr WwTW | 1157 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 328606 | 341750 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AA | LL144AA | ll14 4aa | ll144aa | Wrexham | Wrecsam | Abenbury WwTW | 4927 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331643 | 348780 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AB | LL144AB | ll14 4ab | ll144ab | Wrexham | Wrecsam | Abenbury WwTW | 5048 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331519 | 348734 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AD | LL144AD | ll14 4ad | ll144ad | Wrexham | Wrecsam | Abenbury WwTW | 5196 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331372 | 348757 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AE | LL144AE | ll14 4ae | ll144ae | Wrexham | Wrecsam | Abenbury WwTW | 5003 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331572 | 348838 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AF | LL144AF | ll14 4af | ll144af | Wrexham | Wrecsam | Abenbury WwTW | 5082 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331481 | 348674 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AG | LL144AG | ll14 4ag | ll144ag | Wrexham | Wrecsam | Abenbury WwTW | 5316 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331255 | 348799 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AH | LL144AH | ll14 4ah | ll144ah | Wrexham | Wrecsam | Abenbury WwTW | 5316 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331249 | 348709 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AJ | LL144AJ | ll14 4aj | ll144aj | Wrexham | Wrecsam | Abenbury WwTW | 5271 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331290 | 348643 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AL | LL144AL | ll14 4al | ll144al | Wrexham | Wrecsam | Abenbury WwTW | 5366 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331193 | 348594 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AN | LL144AN | ll14 4an | ll144an | Wrexham | Wrecsam | Abenbury WwTW | 5180 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331382 | 348648 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AP | LL144AP | ll14 4ap | ll144ap | Wrexham | Wrecsam | Abenbury WwTW | 5384 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331179 | 348674 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AQ | LL144AQ | ll14 4aq | ll144aq | Wrexham | Wrecsam | Abenbury WwTW | 5108 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331458 | 348726 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AR | LL144AR | ll14 4ar | ll144ar | Wrexham | Wrecsam | Abenbury WwTW | 5400 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331165 | 348723 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AS | LL144AS | ll14 4as | ll144as | Wrexham | Wrecsam | Abenbury WwTW | 5404 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331165 | 348775 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AT | LL144AT | ll14 4at | ll144at | Wrexham | Wrecsam | Abenbury WwTW | 5413 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331161 | 348847 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AU | LL144AU | ll14 4au | ll144au | Wrexham | Wrecsam | Abenbury WwTW | 5351 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331225 | 348866 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AW | LL144AW | ll14 4aw | ll144aw | Wrexham | Wrecsam | Abenbury WwTW | 5389 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331171 | 348613 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AX | LL144AX | ll14 4ax | ll144ax | Wrexham | Wrecsam | Abenbury WwTW | 5352 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331218 | 348786 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AY | LL144AY | ll14 4ay | ll144ay | Wrexham | Wrecsam | Abenbury WwTW | 5321 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331252 | 348833 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4AZ | LL144AZ | ll14 4az | ll144az | Wrexham | Wrecsam | Abenbury WwTW | 5380 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331201 | 348921 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BA | LL144BA | ll14 4ba | ll144ba | Wrexham | Wrecsam | Abenbury WwTW | 5295 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331279 | 348839 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BB | LL144BB | ll14 4bb | ll144bb | Wrexham | Wrecsam | Abenbury WwTW | 5257 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331326 | 348940 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BD | LL144BD | ll14 4bd | ll144bd | Wrexham | Wrecsam | Abenbury WwTW | 5188 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331398 | 348958 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BE | LL144BE | ll14 4be | ll144be | Wrexham | Wrecsam | Abenbury WwTW | 5047 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331538 | 348946 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BG | LL144BG | ll14 4bg | ll144bg | Wrexham | Wrecsam | Abenbury WwTW | 5132 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331440 | 348809 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BH | LL144BH | ll14 4bh | ll144bh | Wrexham | Wrecsam | Abenbury WwTW | 5099 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331480 | 348885 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BJ | LL144BJ | ll14 4bj | ll144bj | Wrexham | Wrecsam | Abenbury WwTW | 5605 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 330952 | 348515 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BL | LL144BL | ll14 4bl | ll144bl | Wrexham | Wrecsam | Abenbury WwTW | 5103 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331487 | 348991 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BN | LL144BN | ll14 4bn | ll144bn | Wrexham | Wrecsam | Abenbury WwTW | 5174 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331403 | 348872 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BP | LL144BP | ll14 4bp | ll144bp | Wrexham | Wrecsam | Abenbury WwTW | 4901 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331687 | 348961 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BQ | LL144BQ | ll14 4bq | ll144bq | Wrexham | Wrecsam | Abenbury WwTW | 4965 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331607 | 348806 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BS | LL144BS | ll14 4bs | ll144bs | Wrexham | Wrecsam | Abenbury WwTW | 4797 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331782 | 348871 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BT | LL144BT | ll14 4bt | ll144bt | Wrexham | Wrecsam | Abenbury WwTW | 4890 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331686 | 348844 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BU | LL144BU | ll14 4bu | ll144bu | Wrexham | Wrecsam | Abenbury WwTW | 4923 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331658 | 348905 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BW | LL144BW | ll14 4bw | ll144bw | Wrexham | Wrecsam | Abenbury WwTW | 4986 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331597 | 348923 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BX | LL144BX | ll14 4bx | ll144bx | Wrexham | Wrecsam | Abenbury WwTW | 5013 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331550 | 348677 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4BY | LL144BY | ll14 4by | ll144by | Wrexham | Wrecsam | Abenbury WwTW | 4746 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331845 | 348983 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DA | LL144DA | ll14 4da | ll144da | Wrexham | Wrecsam | Abenbury WwTW | 4732 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331856 | 348954 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DB | LL144DB | ll14 4db | ll144db | Wrexham | Wrecsam | Abenbury WwTW | 5057 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331533 | 348988 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DD | LL144DD | ll14 4dd | ll144dd | Wrexham | Wrecsam | Abenbury WwTW | 4748 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331852 | 349049 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DE | LL144DE | ll14 4de | ll144de | Wrexham | Wrecsam | Abenbury WwTW | 4834 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331785 | 349180 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DF | LL144DF | ll14 4df | ll144df | Wrexham | Wrecsam | Abenbury WwTW | 4865 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331734 | 349047 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DG | LL144DG | ll14 4dg | ll144dg | Wrexham | Wrecsam | Abenbury WwTW | 4594 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 332039 | 349242 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DH | LL144DH | ll14 4dh | ll144dh | Wrexham | Wrecsam | Abenbury WwTW | 4689 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331895 | 348920 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DJ | LL144DJ | ll14 4dj | ll144dj | Wrexham | Wrecsam | Abenbury WwTW | 4710 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331907 | 349163 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DL | LL144DL | ll14 4dl | ll144dl | Wrexham | Wrecsam | Abenbury WwTW | 4986 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331578 | 348690 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DN | LL144DN | ll14 4dn | ll144dn | Wrexham | Wrecsam | Abenbury WwTW | 5134 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331424 | 348542 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DP | LL144DP | ll14 4dp | ll144dp | Wrexham | Wrecsam | Abenbury WwTW | 5253 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 331303 | 348419 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DQ | LL144DQ | ll14 4dq | ll144dq | Wrexham | Wrecsam | Abenbury WwTW | 4742 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331875 | 349165 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DR | LL144DR | ll14 4dr | ll144dr | Wrexham | Wrecsam | Abenbury WwTW | 5545 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 331033 | 347909 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DS | LL144DS | ll14 4ds | ll144ds | Wrexham | Wrecsam | Abenbury WwTW | 6099 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 330502 | 347664 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DT | LL144DT | ll14 4dt | ll144dt | Wrexham | Wrecsam | Abenbury WwTW | 6317 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 330309 | 347464 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DU | LL144DU | ll14 4du | ll144du | Wrexham | Wrecsam | Abenbury WwTW | 6175 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 330427 | 347648 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DW | LL144DW | ll14 4dw | ll144dw | Wrexham | Wrecsam | Abenbury WwTW | 4980 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331581 | 348627 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DX | LL144DX | ll14 4dx | ll144dx | Wrexham | Wrecsam | Abenbury WwTW | 4695 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331911 | 349086 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DY | LL144DY | ll14 4dy | ll144dy | Wrexham | Wrecsam | Abenbury WwTW | 5157 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331402 | 348578 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4DZ | LL144DZ | ll14 4dz | ll144dz | Wrexham | Wrecsam | Abenbury WwTW | 4664 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331939 | 349069 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EA | LL144EA | ll14 4ea | ll144ea | Wrexham | Wrecsam | Abenbury WwTW | 5343 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331214 | 348533 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EB | LL144EB | ll14 4eb | ll144eb | Wrexham | Wrecsam | Abenbury WwTW | 5297 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 331259 | 348479 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4ED | LL144ED | ll14 4ed | ll144ed | Wrexham | Wrecsam | Abenbury WwTW | 5317 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 331239 | 348446 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EE | LL144EE | ll14 4ee | ll144ee | Wrexham | Wrecsam | Abenbury WwTW | 5208 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331349 | 348524 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EF | LL144EF | ll14 4ef | ll144ef | Wrexham | Wrecsam | Abenbury WwTW | 5256 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331303 | 348587 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EG | LL144EG | ll14 4eg | ll144eg | Wrexham | Wrecsam | Abenbury WwTW | 5135 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 331427 | 348149 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EH | LL144EH | ll14 4eh | ll144eh | Wrexham | Wrecsam | Abenbury WwTW | 6072 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 330508 | 347866 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EJ | LL144EJ | ll14 4ej | ll144ej | Wrexham | Wrecsam | Abenbury WwTW | 5500 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 331056 | 348324 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EL | LL144EL | ll14 4el | ll144el | Wrexham | Wrecsam | Abenbury WwTW | 6124 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 330486 | 347596 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EN | LL144EN | ll14 4en | ll144en | Wrexham | Wrecsam | Abenbury WwTW | 6375 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 330227 | 347638 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EP | LL144EP | ll14 4ep | ll144ep | Wrexham | Wrecsam | Abenbury WwTW | 6365 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 330205 | 347989 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EQ | LL144EQ | ll14 4eq | ll144eq | Wrexham | Wrecsam | Abenbury WwTW | 4717 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331883 | 349046 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4ER | LL144ER | ll14 4er | ll144er | Wrexham | Wrecsam | Froncysyllte STW | 6340 | 924 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.22 | 9.19 | 10.15 | 329404 | 347868 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4ES | LL144ES | ll14 4es | ll144es | Wrexham | Wrecsam | Froncysyllte STW | 6553 | 924 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.22 | 9.19 | 10.15 | 329487 | 348064 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4ET | LL144ET | ll14 4et | ll144et | Wrexham | Wrecsam | Froncysyllte STW | 6126 | 924 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.22 | 9.19 | 10.15 | 329068 | 347763 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EU | LL144EU | ll14 4eu | ll144eu | Wrexham | Wrecsam | Abenbury WwTW | 4947 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331660 | 349114 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EW | LL144EW | ll14 4ew | ll144ew | Wrexham | Wrecsam | Froncysyllte STW | 6439 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 329750 | 347831 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EX | LL144EX | ll14 4ex | ll144ex | Wrexham | Wrecsam | Abenbury WwTW | 5116 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331484 | 349076 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EY | LL144EY | ll14 4ey | ll144ey | Wrexham | Wrecsam | Abenbury WwTW | 4892 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331705 | 349038 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4EZ | LL144EZ | ll14 4ez | ll144ez | Wrexham | Wrecsam | Abenbury WwTW | 5048 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331550 | 349055 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4FA | LL144FA | ll14 4fa | ll144fa | Wrexham | Wrecsam | Abenbury WwTW | 5572 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331015 | 348990 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4FB | LL144FB | ll14 4fb | ll144fb | Wrexham | Wrecsam | Abenbury WwTW | 5616 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 330959 | 348868 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4FD | LL144FD | ll14 4fd | ll144fd | Wrexham | Wrecsam | Abenbury WwTW | 5420 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331166 | 348974 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4FE | LL144FE | ll14 4fe | ll144fe | Wrexham | Wrecsam | Abenbury WwTW | 5615 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 330968 | 348952 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4FF | LL144FF | ll14 4ff | ll144ff | Wrexham | Wrecsam | Abenbury WwTW | 5384 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331204 | 348989 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4FG | LL144FG | ll14 4fg | ll144fg | Wrexham | Wrecsam | Abenbury WwTW | 5130 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 331426 | 348410 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4FH | LL144FH | ll14 4fh | ll144fh | Wrexham | Wrecsam | Abenbury WwTW | 5321 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 331235 | 348357 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4FJ | LL144FJ | ll14 4fj | ll144fj | Wrexham | Wrecsam | Abenbury WwTW | 6092 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 330495 | 347793 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4FP | LL144FP | ll14 4fp | ll144fp | Wrexham | Wrecsam | Abenbury WwTW | 6092 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 330495 | 347793 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4GA | LL144GA | ll14 4ga | ll144ga | Wrexham | Wrecsam | Abenbury WwTW | 5426 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 331130 | 348403 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HD | LL144HD | ll14 4hd | ll144hd | Wrexham | Wrecsam | Abenbury WwTW | 4480 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332254 | 349654 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HE | LL144HE | ll14 4he | ll144he | Wrexham | Wrecsam | Abenbury WwTW | 4694 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332100 | 349880 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HF | LL144HF | ll14 4hf | ll144hf | Wrexham | Wrecsam | Abenbury WwTW | 5026 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331605 | 349269 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HG | LL144HG | ll14 4hg | ll144hg | Wrexham | Wrecsam | Abenbury WwTW | 5245 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331390 | 349312 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HJ | LL144HJ | ll14 4hj | ll144hj | Wrexham | Wrecsam | Abenbury WwTW | 5107 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331490 | 349049 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HL | LL144HL | ll14 4hl | ll144hl | Wrexham | Wrecsam | Abenbury WwTW | 5262 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331361 | 349243 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HN | LL144HN | ll14 4hn | ll144hn | Wrexham | Wrecsam | Abenbury WwTW | 5269 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331344 | 349177 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HP | LL144HP | ll14 4hp | ll144hp | Wrexham | Wrecsam | Abenbury WwTW | 5431 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 331270 | 349651 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HQ | LL144HQ | ll14 4hq | ll144hq | Wrexham | Wrecsam | Abenbury WwTW | 4523 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332241 | 349759 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HR | LL144HR | ll14 4hr | ll144hr | Wrexham | Wrecsam | Abenbury WwTW | 4894 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331770 | 349428 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HS | LL144HS | ll14 4hs | ll144hs | Wrexham | Wrecsam | Abenbury WwTW | 5312 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331317 | 349280 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HT | LL144HT | ll14 4ht | ll144ht | Wrexham | Wrecsam | Abenbury WwTW | 5443 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331177 | 349236 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HU | LL144HU | ll14 4hu | ll144hu | Wrexham | Wrecsam | Abenbury WwTW | 5630 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 330959 | 349013 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HX | LL144HX | ll14 4hx | ll144hx | Wrexham | Wrecsam | Abenbury WwTW | 5202 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331398 | 349080 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HY | LL144HY | ll14 4hy | ll144hy | Wrexham | Wrecsam | Froncysyllte STW | 6620 | 924 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.22 | 9.19 | 10.15 | 329310 | 348201 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4HZ | LL144HZ | ll14 4hz | ll144hz | Wrexham | Wrecsam | Abenbury WwTW | 4627 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 331971 | 349031 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4JA | LL144JA | ll14 4ja | ll144ja | Wrexham | Wrecsam | Abenbury WwTW | 4420 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 332265 | 349466 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4JB | LL144JB | ll14 4jb | ll144jb | Wrexham | Wrecsam | Abenbury WwTW | 4390 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332327 | 349581 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4JD | LL144JD | ll14 4jd | ll144jd | Wrexham | Wrecsam | Abenbury WwTW | 4577 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332130 | 349569 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4JE | LL144JE | ll14 4je | ll144je | Wrexham | Wrecsam | Abenbury WwTW | 4450 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332254 | 349544 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4JF | LL144JF | ll14 4jf | ll144jf | Wrexham | Wrecsam | Abenbury WwTW | 4478 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332224 | 349537 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LA | LL144LA | ll14 4la | ll144la | Wrexham | Wrecsam | Froncysyllte STW | 6525 | 924 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.22 | 9.19 | 10.15 | 328882 | 348238 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LB | LL144LB | ll14 4lb | ll144lb | Wrexham | Wrecsam | Froncysyllte STW | 6799 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 327693 | 348732 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LD | LL144LD | ll14 4ld | ll144ld | Wrexham | Wrecsam | Froncysyllte STW | 6348 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 328369 | 348180 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LE | LL144LE | ll14 4le | ll144le | Wrexham | Wrecsam | Froncysyllte STW | 6644 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 327383 | 348596 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LF | LL144LF | ll14 4lf | ll144lf | Wrexham | Wrecsam | Froncysyllte STW | 5738 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 327704 | 347665 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LG | LL144LG | ll14 4lg | ll144lg | Wrexham | Wrecsam | Froncysyllte STW | 7208 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 328750 | 348976 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LH | LL144LH | ll14 4lh | ll144lh | Wrexham | Wrecsam | Abenbury WwTW | 6677 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 329887 | 348714 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LL | LL144LL | ll14 4ll | ll144ll | Wrexham | Wrecsam | Abenbury WwTW | 5981 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 330633 | 349234 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LN | LL144LN | ll14 4ln | ll144ln | Wrexham | Wrecsam | Abenbury WwTW | 6882 | 895 | 700to900 | 1.79 | 1.31 | 0.96 | 16.68 | 8.9 | 9.83 | 329866 | 350016 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LP | LL144LP | ll14 4lp | ll144lp | Wrexham | Wrecsam | Abenbury WwTW | 5946 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 330663 | 349196 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LS | LL144LS | ll14 4ls | ll144ls | Wrexham | Wrecsam | Llanfynydd STW | 6376 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 327839 | 350380 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LT | LL144LT | ll14 4lt | ll144lt | Wrexham | Wrecsam | Llanfynydd STW | 6890 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 327801 | 349865 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LU | LL144LU | ll14 4lu | ll144lu | Wrexham | Wrecsam | Llanfynydd STW | 6449 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 327896 | 350309 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LW | LL144LW | ll14 4lw | ll144lw | Wrexham | Wrecsam | Llanfynydd STW | 7453 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 329176 | 349464 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4LY | LL144LY | ll14 4ly | ll144ly | Wrexham | Wrecsam | Llanfynydd STW | 6917 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 328880 | 349951 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4NB | LL144NB | ll14 4nb | ll144nb | Wrexham | Wrecsam | Llanfynydd STW | 7357 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 327359 | 349400 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4ND | LL144ND | ll14 4nd | ll144nd | Wrexham | Wrecsam | Froncysyllte STW | 7136 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 328082 | 349027 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 4PJ | LL144PJ | ll14 4pj | ll144pj | Wrexham | Wrecsam | Froncysyllte STW | 5927 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 330376 | 346904 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AA | LL145AA | ll14 5aa | ll145aa | Wrexham | Wrecsam | Whitehurst STW | 2656 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 328322 | 337477 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AB | LL145AB | ll14 5ab | ll145ab | Wrexham | Wrecsam | Whitehurst STW | 2227 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 327986 | 338075 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AD | LL145AD | ll14 5ad | ll145ad | Wrexham | Wrecsam | Whitehurst STW | 1580 | 894 | 700to900 | 1.79 | 1.31 | 0.96 | 16.66 | 8.89 | 9.82 | 327759 | 339120 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AE | LL145AE | ll14 5ae | ll145ae | Wrexham | Wrecsam | Pontfadog STW | 2714 | 915 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.05 | 9.1 | 10.05 | 326863 | 338111 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AF | LL145AF | ll14 5af | ll145af | Wrexham | Wrecsam | Pontfadog STW | 2708 | 915 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.05 | 9.1 | 10.05 | 326851 | 338067 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AG | LL145AG | ll14 5ag | ll145ag | Wrexham | Wrecsam | Pontfadog STW | 2217 | 977 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.21 | 9.71 | 10.73 | 326328 | 338947 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AH | LL145AH | ll14 5ah | ll145ah | Wrexham | Wrecsam | Cefn Mawr WwTW | 1475 | 976 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.19 | 9.7 | 10.72 | 327348 | 340229 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AJ | LL145AJ | ll14 5aj | ll145aj | Wrexham | Wrecsam | Whitehurst STW | 2487 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 328678 | 337572 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AL | LL145AL | ll14 5al | ll145al | Wrexham | Wrecsam | Cefn Mawr WwTW | 1138 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 327710 | 340592 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AN | LL145AN | ll14 5an | ll145an | Wrexham | Wrecsam | Whitehurst STW | 1047 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 328138 | 340543 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AP | LL145AP | ll14 5ap | ll145ap | Wrexham | Wrecsam | Whitehurst STW | 776 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 328930 | 340796 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AQ | LL145AQ | ll14 5aq | ll145aq | Wrexham | Wrecsam | Whitehurst STW | 818 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 329507 | 339352 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AR | LL145AR | ll14 5ar | ll145ar | Wrexham | Wrecsam | Whitehurst STW | 1407 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329139 | 341434 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AS | LL145AS | ll14 5as | ll145as | Wrexham | Wrecsam | Whitehurst STW | 393 | 875 | 700to900 | 1.75 | 1.28 | 0.94 | 16.31 | 8.7 | 9.61 | 328687 | 340181 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AT | LL145AT | ll14 5at | ll145at | Wrexham | Wrecsam | Whitehurst STW | 141 | 875 | 700to900 | 1.75 | 1.28 | 0.94 | 16.31 | 8.7 | 9.61 | 328913 | 339997 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AU | LL145AU | ll14 5au | ll145au | Wrexham | Wrecsam | Whitehurst STW | 496 | 875 | 700to900 | 1.75 | 1.28 | 0.94 | 16.31 | 8.7 | 9.61 | 329186 | 339553 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AW | LL145AW | ll14 5aw | ll145aw | Wrexham | Wrecsam | Whitehurst STW | 875 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 328880 | 340888 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AX | LL145AX | ll14 5ax | ll145ax | Wrexham | Wrecsam | Halton WwTW | 758 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330043 | 340060 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AY | LL145AY | ll14 5ay | ll145ay | Wrexham | Wrecsam | Whitehurst STW | 667 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329599 | 339652 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5AZ | LL145AZ | ll14 5az | ll145az | Wrexham | Wrecsam | Whitehurst STW | 1011 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330013 | 339722 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BA | LL145BA | ll14 5ba | ll145ba | Wrexham | Wrecsam | Whitehurst STW | 639 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329687 | 340074 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BB | LL145BB | ll14 5bb | ll145bb | Wrexham | Wrecsam | Halton WwTW | 572 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330140 | 340230 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BD | LL145BD | ll14 5bd | ll145bd | Wrexham | Wrecsam | Halton WwTW | 433 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330232 | 340337 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BE | LL145BE | ll14 5be | ll145be | Wrexham | Wrecsam | Whitehurst STW | 873 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329304 | 339195 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BF | LL145BF | ll14 5bf | ll145bf | Wrexham | Wrecsam | Whitehurst STW | 844 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329430 | 339277 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BG | LL145BG | ll14 5bg | ll145bg | Wrexham | Wrecsam | Halton WwTW | 993 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330239 | 339660 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BH | LL145BH | ll14 5bh | ll145bh | Wrexham | Wrecsam | Halton WwTW | 2025 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 331192 | 338662 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BJ | LL145BJ | ll14 5bj | ll145bj | Wrexham | Wrecsam | Whitehurst STW | 958 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329216 | 339087 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BL | LL145BL | ll14 5bl | ll145bl | Wrexham | Wrecsam | Pontfadog STW | 2336 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 326377 | 337677 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BN | LL145BN | ll14 5bn | ll145bn | Wrexham | Wrecsam | Whitehurst STW | 1000 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329071 | 339031 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BP | LL145BP | ll14 5bp | ll145bp | Wrexham | Wrecsam | Whitehurst STW | 850 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329064 | 339180 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BQ | LL145BQ | ll14 5bq | ll145bq | Wrexham | Wrecsam | Whitehurst STW | 2491 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 328631 | 337575 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BS | LL145BS | ll14 5bs | ll145bs | Wrexham | Wrecsam | Whitehurst STW | 2478 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 328856 | 337560 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BT | LL145BT | ll14 5bt | ll145bt | Wrexham | Wrecsam | Whitehurst STW | 2552 | 882 | 700to900 | 1.77 | 1.29 | 0.95 | 16.44 | 8.77 | 9.69 | 328848 | 337487 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BW | LL145BW | ll14 5bw | ll145bw | Wrexham | Wrecsam | Whitehurst STW | 956 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 328952 | 339079 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BX | LL145BX | ll14 5bx | ll145bx | Wrexham | Wrecsam | Whitehurst STW | 794 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329405 | 339320 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5BZ | LL145BZ | ll14 5bz | ll145bz | Wrexham | Wrecsam | Whitehurst STW | 737 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329353 | 339358 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5DH | LL145DH | ll14 5dh | ll145dh | Wrexham | Wrecsam | Whitehurst STW | 2250 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329174 | 337784 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5DJ | LL145DJ | ll14 5dj | ll145dj | Wrexham | Wrecsam | Whitehurst STW | 836 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329234 | 339215 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5EP | LL145EP | ll14 5ep | ll145ep | Wrexham | Wrecsam | Whitehurst STW | 675 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329239 | 339382 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5EQ | LL145EQ | ll14 5eq | ll145eq | Wrexham | Wrecsam | Whitehurst STW | 725 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329265 | 339338 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5ER | LL145ER | ll14 5er | ll145er | Wrexham | Wrecsam | Whitehurst STW | 706 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329163 | 339333 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5ET | LL145ET | ll14 5et | ll145et | Wrexham | Wrecsam | Whitehurst STW | 2233 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329087 | 337798 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5EU | LL145EU | ll14 5eu | ll145eu | Wrexham | Wrecsam | Whitehurst STW | 2196 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329069 | 337835 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5EY | LL145EY | ll14 5ey | ll145ey | Wrexham | Wrecsam | Whitehurst STW | 2274 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329071 | 337757 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5EZ | LL145EZ | ll14 5ez | ll145ez | Wrexham | Wrecsam | Whitehurst STW | 2321 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329086 | 337710 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HA | LL145HA | ll14 5ha | ll145ha | Wrexham | Wrecsam | Whitehurst STW | 2370 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329071 | 337661 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HB | LL145HB | ll14 5hb | ll145hb | Wrexham | Wrecsam | Whitehurst STW | 2318 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329034 | 337713 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HD | LL145HD | ll14 5hd | ll145hd | Wrexham | Wrecsam | Whitehurst STW | 2452 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329208 | 337584 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HE | LL145HE | ll14 5he | ll145he | Wrexham | Wrecsam | Whitehurst STW | 2464 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329248 | 337575 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HF | LL145HF | ll14 5hf | ll145hf | Wrexham | Wrecsam | Whitehurst STW | 1547 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329027 | 338484 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HL | LL145HL | ll14 5hl | ll145hl | Wrexham | Wrecsam | Whitehurst STW | 1464 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329041 | 338567 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HN | LL145HN | ll14 5hn | ll145hn | Wrexham | Wrecsam | Whitehurst STW | 1354 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 328997 | 338677 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HP | LL145HP | ll14 5hp | ll145hp | Wrexham | Wrecsam | Whitehurst STW | 1141 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 328933 | 338895 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HR | LL145HR | ll14 5hr | ll145hr | Wrexham | Wrecsam | Whitehurst STW | 1085 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329029 | 338946 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HS | LL145HS | ll14 5hs | ll145hs | Wrexham | Wrecsam | Whitehurst STW | 1212 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329015 | 338819 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HT | LL145HT | ll14 5ht | ll145ht | Wrexham | Wrecsam | Whitehurst STW | 1143 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329082 | 338888 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HU | LL145HU | ll14 5hu | ll145hu | Wrexham | Wrecsam | Whitehurst STW | 1064 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329154 | 338971 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HW | LL145HW | ll14 5hw | ll145hw | Wrexham | Wrecsam | Whitehurst STW | 1177 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 328951 | 338858 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HX | LL145HX | ll14 5hx | ll145hx | Wrexham | Wrecsam | Whitehurst STW | 2371 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329111 | 337661 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5HY | LL145HY | ll14 5hy | ll145hy | Wrexham | Wrecsam | Whitehurst STW | 1205 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329184 | 338833 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LA | LL145LA | ll14 5la | ll145la | Wrexham | Wrecsam | Whitehurst STW | 1293 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329114 | 338739 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LB | LL145LB | ll14 5lb | ll145lb | Wrexham | Wrecsam | Whitehurst STW | 1453 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329091 | 338578 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LD | LL145LD | ll14 5ld | ll145ld | Wrexham | Wrecsam | Whitehurst STW | 1334 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329053 | 338696 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LE | LL145LE | ll14 5le | ll145le | Wrexham | Wrecsam | Whitehurst STW | 1385 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329081 | 338646 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LF | LL145LF | ll14 5lf | ll145lf | Wrexham | Wrecsam | Whitehurst STW | 1514 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329204 | 338524 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LG | LL145LG | ll14 5lg | ll145lg | Wrexham | Wrecsam | Whitehurst STW | 1414 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329319 | 338642 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LH | LL145LH | ll14 5lh | ll145lh | Wrexham | Wrecsam | Whitehurst STW | 1460 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329294 | 338591 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LL | LL145LL | ll14 5ll | ll145ll | Wrexham | Wrecsam | Whitehurst STW | 1523 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329284 | 338526 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LN | LL145LN | ll14 5ln | ll145ln | Wrexham | Wrecsam | Whitehurst STW | 1111 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329398 | 338975 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LQ | LL145LQ | ll14 5lq | ll145lq | Wrexham | Wrecsam | Whitehurst STW | 2370 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 328969 | 337662 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LR | LL145LR | ll14 5lr | ll145lr | Wrexham | Wrecsam | Whitehurst STW | 2346 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 328769 | 337702 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LS | LL145LS | ll14 5ls | ll145ls | Wrexham | Wrecsam | Whitehurst STW | 2302 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 328939 | 337731 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LT | LL145LT | ll14 5lt | ll145lt | Wrexham | Wrecsam | Whitehurst STW | 2098 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 328623 | 337977 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LU | LL145LU | ll14 5lu | ll145lu | Wrexham | Wrecsam | Whitehurst STW | 2268 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 328567 | 337815 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LW | LL145LW | ll14 5lw | ll145lw | Wrexham | Wrecsam | Whitehurst STW | 2317 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329152 | 337716 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5LY | LL145LY | ll14 5ly | ll145ly | Wrexham | Wrecsam | Whitehurst STW | 2387 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 328851 | 337652 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NA | LL145NA | ll14 5na | ll145na | Wrexham | Wrecsam | Whitehurst STW | 2038 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329061 | 337993 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5ND | LL145ND | ll14 5nd | ll145nd | Wrexham | Wrecsam | Whitehurst STW | 1926 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329106 | 338105 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NE | LL145NE | ll14 5ne | ll145ne | Wrexham | Wrecsam | Whitehurst STW | 1919 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329179 | 338116 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NF | LL145NF | ll14 5nf | ll145nf | Wrexham | Wrecsam | Whitehurst STW | 1672 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329216 | 338367 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NG | LL145NG | ll14 5ng | ll145ng | Wrexham | Wrecsam | Whitehurst STW | 1592 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329382 | 338474 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NH | LL145NH | ll14 5nh | ll145nh | Wrexham | Wrecsam | Whitehurst STW | 1699 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329392 | 338366 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NJ | LL145NJ | ll14 5nj | ll145nj | Wrexham | Wrecsam | Whitehurst STW | 1691 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329426 | 338382 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NL | LL145NL | ll14 5nl | ll145nl | Wrexham | Wrecsam | Whitehurst STW | 1637 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329499 | 338456 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NN | LL145NN | ll14 5nn | ll145nn | Wrexham | Wrecsam | Whitehurst STW | 1791 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329144 | 338242 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NP | LL145NP | ll14 5np | ll145np | Wrexham | Wrecsam | Whitehurst STW | 1696 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329153 | 338338 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NQ | LL145NQ | ll14 5nq | ll145nq | Wrexham | Wrecsam | Whitehurst STW | 1787 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329272 | 338257 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NR | LL145NR | ll14 5nr | ll145nr | Wrexham | Wrecsam | Whitehurst STW | 1726 | 841 | 700to900 | 1.68 | 1.23 | 0.9 | 15.67 | 8.36 | 9.24 | 329740 | 338449 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NS | LL145NS | ll14 5ns | ll145ns | Wrexham | Wrecsam | Whitehurst STW | 2375 | 841 | 700to900 | 1.68 | 1.23 | 0.9 | 15.67 | 8.36 | 9.24 | 330306 | 338015 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NT | LL145NT | ll14 5nt | ll145nt | Wrexham | Wrecsam | Whitehurst STW | 1818 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 328727 | 338242 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NU | LL145NU | ll14 5nu | ll145nu | Wrexham | Wrecsam | Whitehurst STW | 1680 | 841 | 700to900 | 1.68 | 1.23 | 0.9 | 15.67 | 8.36 | 9.24 | 329560 | 338430 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5NY | LL145NY | ll14 5ny | ll145ny | Wrexham | Wrecsam | Whitehurst STW | 1595 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329406 | 338476 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PA | LL145PA | ll14 5pa | ll145pa | Wrexham | Wrecsam | Whitehurst STW | 2159 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329096 | 337872 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PB | LL145PB | ll14 5pb | ll145pb | Wrexham | Wrecsam | Whitehurst STW | 2074 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329301 | 337972 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PD | LL145PD | ll14 5pd | ll145pd | Wrexham | Wrecsam | Whitehurst STW | 2162 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329252 | 337878 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PE | LL145PE | ll14 5pe | ll145pe | Wrexham | Wrecsam | Whitehurst STW | 2239 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329243 | 337800 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PF | LL145PF | ll14 5pf | ll145pf | Wrexham | Wrecsam | Whitehurst STW | 2224 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329338 | 337825 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PG | LL145PG | ll14 5pg | ll145pg | Wrexham | Wrecsam | Whitehurst STW | 2162 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329383 | 337895 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PH | LL145PH | ll14 5ph | ll145ph | Wrexham | Wrecsam | Whitehurst STW | 2122 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329237 | 337917 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PJ | LL145PJ | ll14 5pj | ll145pj | Wrexham | Wrecsam | Whitehurst STW | 2148 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329342 | 337903 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PL | LL145PL | ll14 5pl | ll145pl | Wrexham | Wrecsam | Whitehurst STW | 2140 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329151 | 337893 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PN | LL145PN | ll14 5pn | ll145pn | Wrexham | Wrecsam | Whitehurst STW | 2165 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329419 | 337897 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PP | LL145PP | ll14 5pp | ll145pp | Wrexham | Wrecsam | Whitehurst STW | 1918 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329256 | 338124 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PQ | LL145PQ | ll14 5pq | ll145pq | Wrexham | Wrecsam | Whitehurst STW | 2205 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329164 | 337829 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PR | LL145PR | ll14 5pr | ll145pr | Wrexham | Wrecsam | Whitehurst STW | 1963 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329462 | 338111 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PS | LL145PS | ll14 5ps | ll145ps | Wrexham | Wrecsam | Whitehurst STW | 1921 | 841 | 700to900 | 1.68 | 1.23 | 0.9 | 15.67 | 8.36 | 9.24 | 329504 | 338164 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PT | LL145PT | ll14 5pt | ll145pt | Wrexham | Wrecsam | Whitehurst STW | 1797 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329432 | 338275 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PU | LL145PU | ll14 5pu | ll145pu | Wrexham | Wrecsam | Whitehurst STW | 1845 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329424 | 338224 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PW | LL145PW | ll14 5pw | ll145pw | Wrexham | Wrecsam | Whitehurst STW | 1940 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329344 | 338113 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5PY | LL145PY | ll14 5py | ll145py | Wrexham | Wrecsam | Whitehurst STW | 1797 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329499 | 338291 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5QB | LL145QB | ll14 5qb | ll145qb | Wrexham | Wrecsam | Whitehurst STW | 1834 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329368 | 338224 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5RA | LL145RA | ll14 5ra | ll145ra | Wrexham | Wrecsam | Whitehurst STW | 770 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329446 | 339370 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5RB | LL145RB | ll14 5rb | ll145rb | Wrexham | Wrecsam | Whitehurst STW | 1860 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329469 | 338218 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5RD | LL145RD | ll14 5rd | ll145rd | Wrexham | Wrecsam | Whitehurst STW | 2094 | 841 | 700to900 | 1.68 | 1.23 | 0.9 | 15.67 | 8.36 | 9.24 | 329710 | 338043 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5RE | LL145RE | ll14 5re | ll145re | Wrexham | Wrecsam | Whitehurst STW | 2080 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329259 | 337961 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5RF | LL145RF | ll14 5rf | ll145rf | Wrexham | Wrecsam | Whitehurst STW | 912 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329416 | 339195 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5RG | LL145RG | ll14 5rg | ll145rg | Wrexham | Wrecsam | Whitehurst STW | 932 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329369 | 339155 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5RL | LL145RL | ll14 5rl | ll145rl | Wrexham | Wrecsam | Whitehurst STW | 2174 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 328348 | 337973 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5SB | LL145SB | ll14 5sb | ll145sb | Wrexham | Wrecsam | Whitehurst STW | 2464 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 328781 | 337582 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 5YG | LL145YG | ll14 5yg | ll145yg | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AB | LL146AB | ll14 6ab | ll146ab | Wrexham | Wrecsam | Halton WwTW | 3310 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330378 | 343895 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AD | LL146AD | ll14 6ad | ll146ad | Wrexham | Wrecsam | Halton WwTW | 3381 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330489 | 343971 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AE | LL146AE | ll14 6ae | ll146ae | Wrexham | Wrecsam | Halton WwTW | 3345 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330521 | 343935 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AF | LL146AF | ll14 6af | ll146af | Wrexham | Wrecsam | Halton WwTW | 3777 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330693 | 344366 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AG | LL146AG | ll14 6ag | ll146ag | Wrexham | Wrecsam | Halton WwTW | 3511 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330674 | 344101 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AH | LL146AH | ll14 6ah | ll146ah | Wrexham | Wrecsam | Halton WwTW | 3639 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330643 | 344229 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AJ | LL146AJ | ll14 6aj | ll146aj | Wrexham | Wrecsam | Halton WwTW | 3818 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330793 | 344403 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AL | LL146AL | ll14 6al | ll146al | Wrexham | Wrecsam | Halton WwTW | 3513 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330592 | 344104 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AN | LL146AN | ll14 6an | ll146an | Wrexham | Wrecsam | Halton WwTW | 3563 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330662 | 344153 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AP | LL146AP | ll14 6ap | ll146ap | Wrexham | Wrecsam | Halton WwTW | 3621 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330530 | 344211 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AQ | LL146AQ | ll14 6aq | ll146aq | Wrexham | Wrecsam | Halton WwTW | 3319 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330631 | 343910 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AR | LL146AR | ll14 6ar | ll146ar | Wrexham | Wrecsam | Halton WwTW | 3737 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330597 | 344328 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AS | LL146AS | ll14 6as | ll146as | Wrexham | Wrecsam | Halton WwTW | 3779 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330529 | 344369 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AT | LL146AT | ll14 6at | ll146at | Wrexham | Wrecsam | Halton WwTW | 3932 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330578 | 344523 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AU | LL146AU | ll14 6au | ll146au | Wrexham | Wrecsam | Halton WwTW | 4005 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330576 | 344596 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AW | LL146AW | ll14 6aw | ll146aw | Wrexham | Wrecsam | Halton WwTW | 3511 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330468 | 344100 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AX | LL146AX | ll14 6ax | ll146ax | Wrexham | Wrecsam | Halton WwTW | 3393 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330676 | 343983 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AY | LL146AY | ll14 6ay | ll146ay | Wrexham | Wrecsam | Halton WwTW | 4054 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330553 | 344645 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6AZ | LL146AZ | ll14 6az | ll146az | Wrexham | Wrecsam | Halton WwTW | 3320 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330573 | 343911 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BA | LL146BA | ll14 6ba | ll146ba | Wrexham | Wrecsam | Halton WwTW | 4061 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330507 | 344651 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BB | LL146BB | ll14 6bb | ll146bb | Wrexham | Wrecsam | Halton WwTW | 4033 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 330482 | 344622 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BD | LL146BD | ll14 6bd | ll146bd | Wrexham | Wrecsam | Halton WwTW | 4109 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330520 | 344699 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BE | LL146BE | ll14 6be | ll146be | Wrexham | Wrecsam | Halton WwTW | 3929 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 330496 | 344519 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BF | LL146BF | ll14 6bf | ll146bf | Wrexham | Wrecsam | Halton WwTW | 3353 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330399 | 343939 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BG | LL146BG | ll14 6bg | ll146bg | Wrexham | Wrecsam | Halton WwTW | 3827 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330504 | 344417 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BH | LL146BH | ll14 6bh | ll146bh | Wrexham | Wrecsam | Halton WwTW | 3723 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330461 | 344312 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BJ | LL146BJ | ll14 6bj | ll146bj | Wrexham | Wrecsam | Halton WwTW | 4157 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330700 | 344746 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BL | LL146BL | ll14 6bl | ll146bl | Wrexham | Wrecsam | Halton WwTW | 3279 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330361 | 343862 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BN | LL146BN | ll14 6bn | ll146bn | Wrexham | Wrecsam | Halton WwTW | 3939 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330627 | 344529 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BP | LL146BP | ll14 6bp | ll146bp | Wrexham | Wrecsam | Halton WwTW | 3864 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330728 | 344452 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BQ | LL146BQ | ll14 6bq | ll146bq | Wrexham | Wrecsam | Halton WwTW | 4077 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330666 | 344667 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BS | LL146BS | ll14 6bs | ll146bs | Wrexham | Wrecsam | Halton WwTW | 4155 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330801 | 344740 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BT | LL146BT | ll14 6bt | ll146bt | Wrexham | Wrecsam | Cefn Mawr WwTW | 3228 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329726 | 343988 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BU | LL146BU | ll14 6bu | ll146bu | Wrexham | Wrecsam | Halton WwTW | 3166 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330305 | 343745 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BW | LL146BW | ll14 6bw | ll146bw | Wrexham | Wrecsam | Halton WwTW | 4084 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330743 | 344671 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BX | LL146BX | ll14 6bx | ll146bx | Wrexham | Wrecsam | Halton WwTW | 3974 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330753 | 344561 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BY | LL146BY | ll14 6by | ll146by | Wrexham | Wrecsam | Halton WwTW | 3878 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330778 | 344464 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6BZ | LL146BZ | ll14 6bz | ll146bz | Wrexham | Wrecsam | Halton WwTW | 4082 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330858 | 344663 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DA | LL146DA | ll14 6da | ll146da | Wrexham | Wrecsam | Halton WwTW | 3193 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330243 | 343766 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DB | LL146DB | ll14 6db | ll146db | Wrexham | Wrecsam | Halton WwTW | 3140 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330327 | 343721 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DD | LL146DD | ll14 6dd | ll146dd | Wrexham | Wrecsam | Halton WwTW | 3097 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330255 | 343671 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DE | LL146DE | ll14 6de | ll146de | Wrexham | Wrecsam | Halton WwTW | 3148 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330210 | 343717 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DF | LL146DF | ll14 6df | ll146df | Wrexham | Wrecsam | Halton WwTW | 3151 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330258 | 343725 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DG | LL146DG | ll14 6dg | ll146dg | Wrexham | Wrecsam | Halton WwTW | 3257 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330189 | 343824 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DH | LL146DH | ll14 6dh | ll146dh | Wrexham | Wrecsam | Halton WwTW | 3249 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330147 | 343811 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DJ | LL146DJ | ll14 6dj | ll146dj | Wrexham | Wrecsam | Halton WwTW | 3104 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330353 | 343686 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DL | LL146DL | ll14 6dl | ll146dl | Wrexham | Wrecsam | Halton WwTW | 3175 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330085 | 343727 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DP | LL146DP | ll14 6dp | ll146dp | Wrexham | Wrecsam | Cefn Mawr WwTW | 2620 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 329443 | 343400 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DQ | LL146DQ | ll14 6dq | ll146dq | Wrexham | Wrecsam | Halton WwTW | 3296 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330278 | 343873 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DR | LL146DR | ll14 6dr | ll146dr | Wrexham | Wrecsam | Halton WwTW | 3341 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330176 | 343907 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DS | LL146DS | ll14 6ds | ll146ds | Wrexham | Wrecsam | Halton WwTW | 3275 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330239 | 343848 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DT | LL146DT | ll14 6dt | ll146dt | Wrexham | Wrecsam | Halton WwTW | 3417 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330124 | 343977 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DU | LL146DU | ll14 6du | ll146du | Wrexham | Wrecsam | Cefn Mawr WwTW | 3284 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329918 | 343865 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DW | LL146DW | ll14 6dw | ll146dw | Wrexham | Wrecsam | Halton WwTW | 2798 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 330181 | 343360 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DX | LL146DX | ll14 6dx | ll146dx | Wrexham | Wrecsam | Halton WwTW | 3200 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330164 | 343763 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6DY | LL146DY | ll14 6dy | ll146dy | Wrexham | Wrecsam | Halton WwTW | 3410 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330027 | 343955 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6EA | LL146EA | ll14 6ea | ll146ea | Wrexham | Wrecsam | Halton WwTW | 3380 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330016 | 343923 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6EB | LL146EB | ll14 6eb | ll146eb | Wrexham | Wrecsam | Cefn Mawr WwTW | 3359 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329840 | 344059 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6ED | LL146ED | ll14 6ed | ll146ed | Wrexham | Wrecsam | Cefn Mawr WwTW | 3229 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329818 | 343894 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6EE | LL146EE | ll14 6ee | ll146ee | Wrexham | Wrecsam | Cefn Mawr WwTW | 3204 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329862 | 343807 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6EF | LL146EF | ll14 6ef | ll146ef | Wrexham | Wrecsam | Cefn Mawr WwTW | 3096 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329689 | 343837 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6EG | LL146EG | ll14 6eg | ll146eg | Wrexham | Wrecsam | Cefn Mawr WwTW | 3019 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329657 | 343759 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6EH | LL146EH | ll14 6eh | ll146eh | Wrexham | Wrecsam | Cefn Mawr WwTW | 2942 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329569 | 343739 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6EJ | LL146EJ | ll14 6ej | ll146ej | Wrexham | Wrecsam | Halton WwTW | 3172 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329965 | 343702 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6EL | LL146EL | ll14 6el | ll146el | Wrexham | Wrecsam | Cefn Mawr WwTW | 2912 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329619 | 343642 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6EN | LL146EN | ll14 6en | ll146en | Wrexham | Wrecsam | Cefn Mawr WwTW | 2611 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 329324 | 343517 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6EP | LL146EP | ll14 6ep | ll146ep | Wrexham | Wrecsam | Cefn Mawr WwTW | 2912 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 329812 | 343401 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6EQ | LL146EQ | ll14 6eq | ll146eq | Wrexham | Wrecsam | Halton WwTW | 2981 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 329914 | 343496 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6ER | LL146ER | ll14 6er | ll146er | Wrexham | Wrecsam | Halton WwTW | 3397 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330441 | 343985 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6ET | LL146ET | ll14 6et | ll146et | Wrexham | Wrecsam | Halton WwTW | 5659 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 331185 | 346217 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HA | LL146HA | ll14 6ha | ll146ha | Wrexham | Wrecsam | Cefn Mawr WwTW | 4676 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 330372 | 345348 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HB | LL146HB | ll14 6hb | ll146hb | Wrexham | Wrecsam | Halton WwTW | 4467 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330884 | 345047 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HD | LL146HD | ll14 6hd | ll146hd | Wrexham | Wrecsam | Halton WwTW | 3932 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 331297 | 344457 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HF | LL146HF | ll14 6hf | ll146hf | Wrexham | Wrecsam | Halton WwTW | 5558 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 331325 | 346098 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HG | LL146HG | ll14 6hg | ll146hg | Wrexham | Wrecsam | Abenbury WwTW | 5562 | 834 | 700to900 | 1.67 | 1.22 | 0.9 | 15.54 | 8.29 | 9.16 | 331132 | 347171 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HJ | LL146HJ | ll14 6hj | ll146hj | Wrexham | Wrecsam | Cefn Mawr WwTW | 4402 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 330228 | 345113 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HL | LL146HL | ll14 6hl | ll146hl | Wrexham | Wrecsam | Erbistock STW | 3467 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 332438 | 343709 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HN | LL146HN | ll14 6hn | ll146hn | Wrexham | Wrecsam | Halton WwTW | 3286 | 819 | 700to900 | 1.64 | 1.2 | 0.88 | 15.26 | 8.14 | 9 | 332423 | 343313 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HP | LL146HP | ll14 6hp | ll146hp | Wrexham | Wrecsam | Erbistock STW | 2246 | 777 | 700to900 | 1.56 | 1.14 | 0.83 | 14.48 | 7.72 | 8.54 | 333230 | 341882 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HR | LL146HR | ll14 6hr | ll146hr | Wrexham | Wrecsam | Erbistock STW | 2191 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 333524 | 341024 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HS | LL146HS | ll14 6hs | ll146hs | Wrexham | Wrecsam | Halton WwTW | 2375 | 775 | 700to900 | 1.55 | 1.14 | 0.83 | 14.44 | 7.7 | 8.51 | 332891 | 341145 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HT | LL146HT | ll14 6ht | ll146ht | Wrexham | Wrecsam | Halton WwTW | 2588 | 777 | 700to900 | 1.56 | 1.14 | 0.83 | 14.48 | 7.72 | 8.54 | 332505 | 342322 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HU | LL146HU | ll14 6hu | ll146hu | Wrexham | Wrecsam | Cefn Mawr WwTW | 4576 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 330409 | 345189 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HW | LL146HW | ll14 6hw | ll146hw | Wrexham | Wrecsam | Erbistock STW | 2775 | 784 | 700to900 | 1.57 | 1.15 | 0.84 | 14.61 | 7.79 | 8.61 | 332806 | 342803 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6HY | LL146HY | ll14 6hy | ll146hy | Wrexham | Wrecsam | Cefn Mawr WwTW | 4929 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330470 | 345593 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LA | LL146LA | ll14 6la | ll146la | Wrexham | Wrecsam | Halton WwTW | 2111 | 837 | 700to900 | 1.68 | 1.23 | 0.9 | 15.6 | 8.32 | 9.2 | 330960 | 342668 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LB | LL146LB | ll14 6lb | ll146lb | Wrexham | Wrecsam | Halton WwTW | 2104 | 837 | 700to900 | 1.68 | 1.23 | 0.9 | 15.6 | 8.32 | 9.2 | 330912 | 342669 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LE | LL146LE | ll14 6le | ll146le | Wrexham | Wrecsam | Halton WwTW | 3161 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330379 | 343745 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LF | LL146LF | ll14 6lf | ll146lf | Wrexham | Wrecsam | Halton WwTW | 2909 | 837 | 700to900 | 1.68 | 1.23 | 0.9 | 15.6 | 8.32 | 9.2 | 330821 | 343490 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LG | LL146LG | ll14 6lg | ll146lg | Wrexham | Wrecsam | Halton WwTW | 3072 | 833 | 700to900 | 1.67 | 1.22 | 0.89 | 15.53 | 8.28 | 9.15 | 330735 | 343659 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LH | LL146LH | ll14 6lh | ll146lh | Wrexham | Wrecsam | Halton WwTW | 2864 | 837 | 700to900 | 1.68 | 1.23 | 0.9 | 15.6 | 8.32 | 9.2 | 331497 | 343305 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LJ | LL146LJ | ll14 6lj | ll146lj | Wrexham | Wrecsam | Halton WwTW | 2055 | 837 | 700to900 | 1.68 | 1.23 | 0.9 | 15.6 | 8.32 | 9.2 | 330915 | 342619 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LL | LL146LL | ll14 6ll | ll146ll | Wrexham | Wrecsam | Halton WwTW | 2788 | 837 | 700to900 | 1.68 | 1.23 | 0.9 | 15.6 | 8.32 | 9.2 | 331033 | 343342 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LN | LL146LN | ll14 6ln | ll146ln | Wrexham | Wrecsam | Halton WwTW | 2544 | 819 | 700to900 | 1.64 | 1.2 | 0.88 | 15.26 | 8.14 | 9 | 331571 | 342935 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LP | LL146LP | ll14 6lp | ll146lp | Wrexham | Wrecsam | Halton WwTW | 1833 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 331597 | 342118 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LQ | LL146LQ | ll14 6lq | ll146lq | Wrexham | Wrecsam | Halton WwTW | 2044 | 837 | 700to900 | 1.68 | 1.23 | 0.9 | 15.6 | 8.32 | 9.2 | 330893 | 342611 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LR | LL146LR | ll14 6lr | ll146lr | Wrexham | Wrecsam | Halton WwTW | 1234 | 832 | 700to900 | 1.67 | 1.22 | 0.89 | 15.51 | 8.27 | 9.14 | 331201 | 341659 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LS | LL146LS | ll14 6ls | ll146ls | Wrexham | Wrecsam | Halton WwTW | 1383 | 832 | 700to900 | 1.67 | 1.22 | 0.89 | 15.51 | 8.27 | 9.14 | 330810 | 341956 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LT | LL146LT | ll14 6lt | ll146lt | Wrexham | Wrecsam | Halton WwTW | 1113 | 798 | 700to900 | 1.6 | 1.17 | 0.86 | 14.87 | 7.93 | 8.77 | 331591 | 341061 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LU | LL146LU | ll14 6lu | ll146lu | Wrexham | Wrecsam | Halton WwTW | 900 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 331192 | 341254 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LW | LL146LW | ll14 6lw | ll146lw | Wrexham | Wrecsam | Halton WwTW | 1810 | 832 | 700to900 | 1.67 | 1.22 | 0.89 | 15.51 | 8.27 | 9.14 | 331347 | 342232 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6LX | LL146LX | ll14 6lx | ll146lx | Wrexham | Wrecsam | Halton WwTW | 3146 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330484 | 343735 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NB | LL146NB | ll14 6nb | ll146nb | Wrexham | Wrecsam | Halton WwTW | 3270 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330334 | 343851 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6ND | LL146ND | ll14 6nd | ll146nd | Wrexham | Wrecsam | Halton WwTW | 3289 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330342 | 343871 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NH | LL146NH | ll14 6nh | ll146nh | Wrexham | Wrecsam | Halton WwTW | 3280 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330337 | 343862 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NJ | LL146NJ | ll14 6nj | ll146nj | Wrexham | Wrecsam | Halton WwTW | 3404 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330255 | 343979 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NL | LL146NL | ll14 6nl | ll146nl | Wrexham | Wrecsam | Halton WwTW | 3438 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330422 | 344025 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NN | LL146NN | ll14 6nn | ll146nn | Wrexham | Wrecsam | Halton WwTW | 3317 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330267 | 343893 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NP | LL146NP | ll14 6np | ll146np | Wrexham | Wrecsam | Halton WwTW | 3475 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330402 | 344061 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NQ | LL146NQ | ll14 6nq | ll146nq | Wrexham | Wrecsam | Halton WwTW | 3343 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330356 | 343926 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NR | LL146NR | ll14 6nr | ll146nr | Wrexham | Wrecsam | Halton WwTW | 3457 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330385 | 344042 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NS | LL146NS | ll14 6ns | ll146ns | Wrexham | Wrecsam | Halton WwTW | 3432 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330339 | 344014 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NT | LL146NT | ll14 6nt | ll146nt | Wrexham | Wrecsam | Halton WwTW | 3404 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330382 | 343989 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NU | LL146NU | ll14 6nu | ll146nu | Wrexham | Wrecsam | Halton WwTW | 3492 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330281 | 344070 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NW | LL146NW | ll14 6nw | ll146nw | Wrexham | Wrecsam | Halton WwTW | 3506 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330416 | 344093 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NX | LL146NX | ll14 6nx | ll146nx | Wrexham | Wrecsam | Halton WwTW | 3388 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330293 | 343966 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6NY | LL146NY | ll14 6ny | ll146ny | Wrexham | Wrecsam | Halton WwTW | 3465 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330336 | 344047 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PA | LL146PA | ll14 6pa | ll146pa | Wrexham | Wrecsam | Halton WwTW | 3493 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330332 | 344075 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PB | LL146PB | ll14 6pb | ll146pb | Wrexham | Wrecsam | Halton WwTW | 3525 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330320 | 344106 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PD | LL146PD | ll14 6pd | ll146pd | Wrexham | Wrecsam | Halton WwTW | 3522 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330295 | 344101 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PE | LL146PE | ll14 6pe | ll146pe | Wrexham | Wrecsam | Halton WwTW | 3588 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330416 | 344175 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PF | LL146PF | ll14 6pf | ll146pf | Wrexham | Wrecsam | Halton WwTW | 3635 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330407 | 344222 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PG | LL146PG | ll14 6pg | ll146pg | Wrexham | Wrecsam | Halton WwTW | 3521 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330375 | 344106 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PH | LL146PH | ll14 6ph | ll146ph | Wrexham | Wrecsam | Halton WwTW | 3563 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330394 | 344149 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PL | LL146PL | ll14 6pl | ll146pl | Wrexham | Wrecsam | Halton WwTW | 3621 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330424 | 344208 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PN | LL146PN | ll14 6pn | ll146pn | Wrexham | Wrecsam | Halton WwTW | 3527 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330357 | 344111 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PP | LL146PP | ll14 6pp | ll146pp | Wrexham | Wrecsam | Halton WwTW | 3666 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330377 | 344251 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PS | LL146PS | ll14 6ps | ll146ps | Wrexham | Wrecsam | Halton WwTW | 3997 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 330362 | 344582 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PT | LL146PT | ll14 6pt | ll146pt | Wrexham | Wrecsam | Halton WwTW | 4102 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 330395 | 344688 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PU | LL146PU | ll14 6pu | ll146pu | Wrexham | Wrecsam | Cefn Mawr WwTW | 4656 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 330202 | 345454 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PW | LL146PW | ll14 6pw | ll146pw | Wrexham | Wrecsam | Halton WwTW | 3594 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330451 | 344182 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6PY | LL146PY | ll14 6py | ll146py | Wrexham | Wrecsam | Cefn Mawr WwTW | 4425 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 330153 | 345201 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6RA | LL146RA | ll14 6ra | ll146ra | Wrexham | Wrecsam | Cefn Mawr WwTW | 4418 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 330117 | 345220 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6RB | LL146RB | ll14 6rb | ll146rb | Wrexham | Wrecsam | Froncysyllte STW | 4555 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329793 | 345639 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6RD | LL146RD | ll14 6rd | ll146rd | Wrexham | Wrecsam | Cefn Mawr WwTW | 3964 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 329856 | 344849 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6RE | LL146RE | ll14 6re | ll146re | Wrexham | Wrecsam | Cefn Mawr WwTW | 3744 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 329709 | 344684 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6RF | LL146RF | ll14 6rf | ll146rf | Wrexham | Wrecsam | Cefn Mawr WwTW | 3666 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329884 | 344440 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6RG | LL146RG | ll14 6rg | ll146rg | Wrexham | Wrecsam | Cefn Mawr WwTW | 4107 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 330040 | 344886 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6RH | LL146RH | ll14 6rh | ll146rh | Wrexham | Wrecsam | Cefn Mawr WwTW | 3326 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329508 | 344311 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6RJ | LL146RJ | ll14 6rj | ll146rj | Wrexham | Wrecsam | Cefn Mawr WwTW | 3348 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329763 | 344119 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6RL | LL146RL | ll14 6rl | ll146rl | Wrexham | Wrecsam | Froncysyllte STW | 3409 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 329242 | 344619 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6RN | LL146RN | ll14 6rn | ll146rn | Wrexham | Wrecsam | Froncysyllte STW | 2362 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 328638 | 343760 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6RP | LL146RP | ll14 6rp | ll146rp | Wrexham | Wrecsam | Cefn Mawr WwTW | 3397 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329808 | 344144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6RW | LL146RW | ll14 6rw | ll146rw | Wrexham | Wrecsam | Cefn Mawr WwTW | 2837 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 329491 | 343669 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6TA | LL146TA | ll14 6ta | ll146ta | Wrexham | Wrecsam | Halton WwTW | 3049 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 329988 | 343582 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6TB | LL146TB | ll14 6tb | ll146tb | Wrexham | Wrecsam | Halton WwTW | 2998 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330035 | 343539 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6TD | LL146TD | ll14 6td | ll146td | Wrexham | Wrecsam | Halton WwTW | 3054 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330171 | 343617 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6TE | LL146TE | ll14 6te | ll146te | Wrexham | Wrecsam | Halton WwTW | 3008 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330096 | 343559 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6TF | LL146TF | ll14 6tf | ll146tf | Wrexham | Wrecsam | Halton WwTW | 3071 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330175 | 343635 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6TG | LL146TG | ll14 6tg | ll146tg | Wrexham | Wrecsam | Halton WwTW | 3043 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 330238 | 343614 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 6YY | LL146YY | ll14 6yy | ll146yy | Wrexham | Wrecsam | Halton WwTW | 3957 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 330882 | 344536 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL15 2RN | LL152RN | ll15 2rn | ll152rn | Denbighshire | Sir Ddinbych | Bryneglwys STW | 3709 | 1002 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.68 | 9.96 | 11.01 | 310549 | 347480 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL16 5SP | LL165SP | ll16 5sp | ll165sp | Denbighshire | Sir Ddinbych | Alwen Septic Tank | 4175 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 293778 | 356085 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7AA | LL207AA | ll20 7aa | ll207aa | Wrexham | Wrecsam | Glynceiriog STW | 551 | 1113 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.74 | 11.06 | 12.23 | 321163 | 337326 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AB | LL207AB | ll20 7ab | ll207ab | Wrexham | Wrecsam | Glynceiriog STW | 227 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 321143 | 337729 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AD | LL207AD | ll20 7ad | ll207ad | Wrexham | Wrecsam | Dolywern STW | 390 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 322058 | 337328 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AE | LL207AE | ll20 7ae | ll207ae | Wrexham | Wrecsam | Dolywern STW | 431 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 322014 | 337313 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AF | LL207AF | ll20 7af | ll207af | Wrexham | Wrecsam | Dolywern STW | 298 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 322147 | 337198 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AG | LL207AG | ll20 7ag | ll207ag | Wrexham | Wrecsam | Dolywern STW | 557 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 321997 | 337587 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AH | LL207AH | ll20 7ah | ll207ah | Wrexham | Wrecsam | Dolywern STW | 741 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 323011 | 337722 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AJ | LL207AJ | ll20 7aj | ll207aj | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 1680 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 317245 | 343825 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7AL | LL207AL | ll20 7al | ll207al | Wrexham | Wrecsam | Dolywern STW | 1028 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 323210 | 337931 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AN | LL207AN | ll20 7an | ll207an | Wrexham | Wrecsam | Pontfadog STW | 969 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 323303 | 338008 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AP | LL207AP | ll20 7ap | ll207ap | Wrexham | Wrecsam | Pontfadog STW | 553 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 323645 | 338268 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AR | LL207AR | ll20 7ar | ll207ar | Wrexham | Wrecsam | Pontfadog STW | 608 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 323592 | 338251 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AS | LL207AS | ll20 7as | ll207as | Wrexham | Wrecsam | Pontfadog STW | 652 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 323523 | 338365 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AT | LL207AT | ll20 7at | ll207at | Wrexham | Wrecsam | Pontfadog STW | 1025 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 325109 | 338849 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AU | LL207AU | ll20 7au | ll207au | Wrexham | Wrecsam | Pontfadog STW | 710 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 323665 | 337941 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AW | LL207AW | ll20 7aw | ll207aw | Wrexham | Wrecsam | Pontfadog STW | 708 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 323498 | 338219 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AX | LL207AX | ll20 7ax | ll207ax | Wrexham | Wrecsam | Pontfadog STW | 801 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 323406 | 338201 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7AY | LL207AY | ll20 7ay | ll207ay | Wrexham | Wrecsam | Dolywern STW | 235 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 322448 | 337015 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7BA | LL207BA | ll20 7ba | ll207ba | Wrexham | Wrecsam | Dolywern STW | 301 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 322194 | 337076 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7BB | LL207BB | ll20 7bb | ll207bb | Wrexham | Wrecsam | Dolywern STW | 226 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 322336 | 337049 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7BD | LL207BD | ll20 7bd | ll207bd | Wrexham | Wrecsam | Dolywern STW | 1281 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 323277 | 336281 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7BE | LL207BE | ll20 7be | ll207be | Wrexham | Wrecsam | Dolywern STW | 1047 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 322326 | 336210 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7BG | LL207BG | ll20 7bg | ll207bg | Wrexham | Wrecsam | Dolywern STW | 673 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 321985 | 336754 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7BH | LL207BH | ll20 7bh | ll207bh | Wrexham | Wrecsam | Dolywern STW | 188 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 322309 | 337115 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7BJ | LL207BJ | ll20 7bj | ll207bj | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 1219 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 317954 | 345421 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7BL | LL207BL | ll20 7bl | ll207bl | Wrexham | Wrecsam | Dolywern STW | 351 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 322123 | 337099 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7BN | LL207BN | ll20 7bn | ll207bn | Wrexham | Wrecsam | Pontfadog STW | 876 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 323370 | 338083 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7BP | LL207BP | ll20 7bp | ll207bp | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2241 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321354 | 341502 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7BS | LL207BS | ll20 7bs | ll207bs | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2389 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 321373 | 341143 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7BT | LL207BT | ll20 7bt | ll207bt | Denbighshire | Sir Ddinbych | Glynceiriog STW | 2336 | 1154 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.51 | 11.47 | 12.68 | 319778 | 339856 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7BU | LL207BU | ll20 7bu | ll207bu | Wrexham | Wrecsam | Glynceiriog STW | 1606 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320484 | 339369 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7BW | LL207BW | ll20 7bw | ll207bw | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2021 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321557 | 341586 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7BX | LL207BX | ll20 7bx | ll207bx | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2110 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 321507 | 341481 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7BY | LL207BY | ll20 7by | ll207by | Wrexham | Wrecsam | Pandy STW | 1041 | 1228 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.89 | 12.21 | 13.49 | 320535 | 336474 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DA | LL207DA | ll20 7da | ll207da | Wrexham | Wrecsam | Glynceiriog STW | 1074 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 319867 | 337851 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DB | LL207DB | ll20 7db | ll207db | Wrexham | Wrecsam | Pandy STW | 2329 | 1226 | 1200to1500 | 2.45 | 1.8 | 1.32 | 22.85 | 12.19 | 13.47 | 317702 | 337109 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DD | LL207DD | ll20 7dd | ll207dd | Wrexham | Wrecsam | Pandy STW | 3829 | 1278 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.82 | 12.7 | 14.04 | 316109 | 337257 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DE | LL207DE | ll20 7de | ll207de | Wrexham | Wrecsam | Pandy STW | 2759 | 1263 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.54 | 12.55 | 13.88 | 318077 | 338124 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DF | LL207DF | ll20 7df | ll207df | Wrexham | Wrecsam | Glynceiriog STW | 1840 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 319239 | 338531 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DG | LL207DG | ll20 7dg | ll207dg | Denbighshire | Sir Ddinbych | Pontfadog STW | 1887 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 322957 | 339885 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7DH | LL207DH | ll20 7dh | ll207dh | Wrexham | Wrecsam | Dolywern STW | 1610 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 322296 | 338853 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DJ | LL207DJ | ll20 7dj | ll207dj | Wrexham | Wrecsam | Froncysyllte STW | 1527 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 325864 | 342842 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DL | LL207DL | ll20 7dl | ll207dl | Wrexham | Wrecsam | Pandy STW | 1163 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 318942 | 336779 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DN | LL207DN | ll20 7dn | ll207dn | Wrexham | Wrecsam | Glynceiriog STW | 679 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320379 | 338213 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DP | LL207DP | ll20 7dp | ll207dp | Wrexham | Wrecsam | Glynceiriog STW | 463 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 320545 | 338071 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DQ | LL207DQ | ll20 7dq | ll207dq | Wrexham | Wrecsam | Froncysyllte STW | 1580 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 325772 | 342799 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DR | LL207DR | ll20 7dr | ll207dr | Wrexham | Wrecsam | Glynceiriog STW | 487 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 320513 | 338064 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DS | LL207DS | ll20 7ds | ll207ds | Wrexham | Wrecsam | Glynceiriog STW | 381 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 320608 | 338016 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DT | LL207DT | ll20 7dt | ll207dt | Wrexham | Wrecsam | Glynceiriog STW | 504 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320476 | 338026 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DU | LL207DU | ll20 7du | ll207du | Wrexham | Wrecsam | Glynceiriog STW | 543 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320442 | 338045 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DW | LL207DW | ll20 7dw | ll207dw | Wrexham | Wrecsam | Glynceiriog STW | 570 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320463 | 338142 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7DY | LL207DY | ll20 7dy | ll207dy | Wrexham | Wrecsam | Glynceiriog STW | 550 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320452 | 338084 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EA | LL207EA | ll20 7ea | ll207ea | Wrexham | Wrecsam | Glynceiriog STW | 605 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320389 | 338080 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EB | LL207EB | ll20 7eb | ll207eb | Wrexham | Wrecsam | Glynceiriog STW | 592 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320408 | 338090 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7ED | LL207ED | ll20 7ed | ll207ed | Wrexham | Wrecsam | Glynceiriog STW | 613 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320389 | 338098 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EE | LL207EE | ll20 7ee | ll207ee | Wrexham | Wrecsam | Glynceiriog STW | 630 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320367 | 338091 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EF | LL207EF | ll20 7ef | ll207ef | Wrexham | Wrecsam | Glynceiriog STW | 679 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320338 | 338144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EG | LL207EG | ll20 7eg | ll207eg | Wrexham | Wrecsam | Glynceiriog STW | 640 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320373 | 338127 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EH | LL207EH | ll20 7eh | ll207eh | Wrexham | Wrecsam | Glynceiriog STW | 709 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320240 | 337943 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EJ | LL207EJ | ll20 7ej | ll207ej | Wrexham | Wrecsam | Froncysyllte STW | 1332 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 325979 | 342662 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EL | LL207EL | ll20 7el | ll207el | Wrexham | Wrecsam | Glynceiriog STW | 672 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320281 | 337959 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EN | LL207EN | ll20 7en | ll207en | Wrexham | Wrecsam | Glynceiriog STW | 693 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320253 | 337917 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EP | LL207EP | ll20 7ep | ll207ep | Wrexham | Wrecsam | Glynceiriog STW | 697 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320247 | 337902 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EQ | LL207EQ | ll20 7eq | ll207eq | Wrexham | Wrecsam | Glynceiriog STW | 868 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320074 | 337770 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7ER | LL207ER | ll20 7er | ll207er | Wrexham | Wrecsam | Glynceiriog STW | 697 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320244 | 337866 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7ES | LL207ES | ll20 7es | ll207es | Wrexham | Wrecsam | Glynceiriog STW | 716 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320224 | 337830 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7ET | LL207ET | ll20 7et | ll207et | Wrexham | Wrecsam | Glynceiriog STW | 778 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320163 | 337801 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EU | LL207EU | ll20 7eu | ll207eu | Wrexham | Wrecsam | Glynceiriog STW | 811 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320136 | 337722 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EW | LL207EW | ll20 7ew | ll207ew | Wrexham | Wrecsam | Glynceiriog STW | 676 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320269 | 337906 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7EY | LL207EY | ll20 7ey | ll207ey | Wrexham | Wrecsam | Glynceiriog STW | 688 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320255 | 337774 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7FB | LL207FB | ll20 7fb | ll207fb | Wrexham | Wrecsam | Glynceiriog STW | 722 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320218 | 337821 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HA | LL207HA | ll20 7ha | ll207ha | Wrexham | Wrecsam | Glynceiriog STW | 660 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320284 | 337764 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HB | LL207HB | ll20 7hb | ll207hb | Wrexham | Wrecsam | Glynceiriog STW | 802 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320196 | 337531 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HD | LL207HD | ll20 7hd | ll207hd | Wrexham | Wrecsam | Glynceiriog STW | 682 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320283 | 337649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HE | LL207HE | ll20 7he | ll207he | Wrexham | Wrecsam | Glynceiriog STW | 642 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320299 | 337864 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HF | LL207HF | ll20 7hf | ll207hf | Wrexham | Wrecsam | Glynceiriog STW | 435 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 320513 | 337913 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HG | LL207HG | ll20 7hg | ll207hg | Wrexham | Wrecsam | Glynceiriog STW | 591 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320353 | 337894 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HH | LL207HH | ll20 7hh | ll207hh | Wrexham | Wrecsam | Glynceiriog STW | 302 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 320707 | 338022 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HJ | LL207HJ | ll20 7hj | ll207hj | Wrexham | Wrecsam | Glynceiriog STW | 674 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320267 | 337860 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HL | LL207HL | ll20 7hl | ll207hl | Wrexham | Wrecsam | Glynceiriog STW | 358 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 320592 | 337915 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HN | LL207HN | ll20 7hn | ll207hn | Wrexham | Wrecsam | Glynceiriog STW | 326 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 320636 | 337947 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HP | LL207HP | ll20 7hp | ll207hp | Wrexham | Wrecsam | Glynceiriog STW | 612 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320362 | 338030 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HR | LL207HR | ll20 7hr | ll207hr | Wrexham | Wrecsam | Glynceiriog STW | 580 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320360 | 337836 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HS | LL207HS | ll20 7hs | ll207hs | Wrexham | Wrecsam | Pandy STW | 487 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 319483 | 335435 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HT | LL207HT | ll20 7ht | ll207ht | Wrexham | Wrecsam | Tregeiriog STW | 854 | 1222 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.78 | 12.15 | 13.43 | 318577 | 334187 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HU | LL207HU | ll20 7hu | ll207hu | Wrexham | Wrecsam | Tregeiriog STW | 285 | 1228 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.89 | 12.21 | 13.49 | 317683 | 333488 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HW | LL207HW | ll20 7hw | ll207hw | Wrexham | Wrecsam | Glynceiriog STW | 470 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 321017 | 338294 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7HY | LL207HY | ll20 7hy | ll207hy | Wrexham | Wrecsam | Tregeiriog STW | 220 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 317790 | 333799 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7LA | LL207LA | ll20 7la | ll207la | Wrexham | Wrecsam | Tregeiriog STW | 401 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 317714 | 333968 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7LB | LL207LB | ll20 7lb | ll207lb | Wrexham | Wrecsam | Llanarmon Dc STW | 599 | 1302 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.27 | 12.94 | 14.3 | 316124 | 333449 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7LD | LL207LD | ll20 7ld | ll207ld | Wrexham | Wrecsam | Llanarmon Dc STW | 300 | 1302 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.27 | 12.94 | 14.3 | 315674 | 332823 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7LE | LL207LE | ll20 7le | ll207le | Wrexham | Wrecsam | Llanarmon Dc STW | 432 | 1302 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.27 | 12.94 | 14.3 | 315540 | 332828 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7LF | LL207LF | ll20 7lf | ll207lf | Wrexham | Wrecsam | Llanarmon Dc STW | 472 | 1302 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.27 | 12.94 | 14.3 | 315577 | 332608 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7LG | LL207LG | ll20 7lg | ll207lg | Wrexham | Wrecsam | Llanarmon Dc STW | 610 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 316501 | 332571 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7LH | LL207LH | ll20 7lh | ll207lh | Wrexham | Wrecsam | Llanarmon Dc STW | 2918 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 313376 | 334204 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7LJ | LL207LJ | ll20 7lj | ll207lj | Wrexham | Wrecsam | Llanarmon Dc STW | 454 | 1302 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.27 | 12.94 | 14.3 | 315516 | 332856 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7LL | LL207LL | ll20 7ll | ll207ll | Wrexham | Wrecsam | Llanarmon Dc STW | 2120 | 1303 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.29 | 12.95 | 14.32 | 314592 | 331260 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7LP | LL207LP | ll20 7lp | ll207lp | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2618 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 319990 | 342201 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7LR | LL207LR | ll20 7lr | ll207lr | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2514 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 320353 | 342564 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7LS | LL207LS | ll20 7ls | ll207ls | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2194 | 1078 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.09 | 10.72 | 11.84 | 319097 | 342350 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7LT | LL207LT | ll20 7lt | ll207lt | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2491 | 1078 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.09 | 10.72 | 11.84 | 318828 | 342029 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7LU | LL207LU | ll20 7lu | ll207lu | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 3502 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 319567 | 341109 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7LY | LL207LY | ll20 7ly | ll207ly | Wrexham | Wrecsam | Glynceiriog STW | 881 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320275 | 338407 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NA | LL207NA | ll20 7na | ll207na | Wrexham | Wrecsam | Glynceiriog STW | 826 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320381 | 338438 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NB | LL207NB | ll20 7nb | ll207nb | Wrexham | Wrecsam | Glynceiriog STW | 817 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320409 | 338451 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7ND | LL207ND | ll20 7nd | ll207nd | Wrexham | Wrecsam | Glynceiriog STW | 857 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320497 | 338563 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NE | LL207NE | ll20 7ne | ll207ne | Wrexham | Wrecsam | Glynceiriog STW | 873 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320287 | 338409 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NF | LL207NF | ll20 7nf | ll207nf | Wrexham | Wrecsam | Glynceiriog STW | 914 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 320093 | 337487 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NG | LL207NG | ll20 7ng | ll207ng | Wrexham | Wrecsam | Glynceiriog STW | 1010 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 320064 | 337328 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NH | LL207NH | ll20 7nh | ll207nh | Wrexham | Wrecsam | Glynceiriog STW | 1082 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 320054 | 337210 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NJ | LL207NJ | ll20 7nj | ll207nj | Wrexham | Wrecsam | Glynceiriog STW | 894 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 320067 | 337637 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NL | LL207NL | ll20 7nl | ll207nl | Wrexham | Wrecsam | Glynceiriog STW | 1101 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 319869 | 337578 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NN | LL207NN | ll20 7nn | ll207nn | Wrexham | Wrecsam | Pandy STW | 929 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 319747 | 336806 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NP | LL207NP | ll20 7np | ll207np | Wrexham | Wrecsam | Pandy STW | 651 | 1231 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.94 | 12.24 | 13.52 | 319878 | 336500 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NR | LL207NR | ll20 7nr | ll207nr | Wrexham | Wrecsam | Glynceiriog STW | 1183 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 320065 | 337034 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NS | LL207NS | ll20 7ns | ll207ns | Wrexham | Wrecsam | Pandy STW | 1178 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 320056 | 336996 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NT | LL207NT | ll20 7nt | ll207nt | Wrexham | Wrecsam | Pandy STW | 238 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 319443 | 335895 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NU | LL207NU | ll20 7nu | ll207nu | Wrexham | Wrecsam | Pandy STW | 82 | 1231 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.94 | 12.24 | 13.52 | 319614 | 335928 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NW | LL207NW | ll20 7nw | ll207nw | Wrexham | Wrecsam | Pandy STW | 1206 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 319992 | 337045 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7NY | LL207NY | ll20 7ny | ll207ny | Wrexham | Wrecsam | Pandy STW | 174 | 1231 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.94 | 12.24 | 13.52 | 319508 | 335904 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7PA | LL207PA | ll20 7pa | ll207pa | Wrexham | Wrecsam | Pandy STW | 813 | 1231 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.94 | 12.24 | 13.52 | 319630 | 335069 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7PB | LL207PB | ll20 7pb | ll207pb | Wrexham | Wrecsam | Pandy STW | 635 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 319045 | 335896 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7PD | LL207PD | ll20 7pd | ll207pd | Wrexham | Wrecsam | Pandy STW | 393 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 319349 | 336091 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7PE | LL207PE | ll20 7pe | ll207pe | Wrexham | Wrecsam | Pandy STW | 250 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 319470 | 336016 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7PF | LL207PF | ll20 7pf | ll207pf | Wrexham | Wrecsam | Froncysyllte STW | 468 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 327024 | 342420 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7PG | LL207PG | ll20 7pg | ll207pg | Denbighshire | Sir Ddinbych | Llangollen WwTW | 876 | 976 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.19 | 9.7 | 10.72 | 322691 | 341889 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7PH | LL207PH | ll20 7ph | ll207ph | Denbighshire | Sir Ddinbych | Llangollen WwTW | 740 | 976 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.19 | 9.7 | 10.72 | 322946 | 341810 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7PL | LL207PL | ll20 7pl | ll207pl | Denbighshire | Sir Ddinbych | Llangollen WwTW | 943 | 976 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.19 | 9.7 | 10.72 | 322658 | 341820 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7PN | LL207PN | ll20 7pn | ll207pn | Denbighshire | Sir Ddinbych | Llangollen WwTW | 924 | 976 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.19 | 9.7 | 10.72 | 322800 | 341693 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7PP | LL207PP | ll20 7pp | ll207pp | Denbighshire | Sir Ddinbych | Llangollen WwTW | 910 | 976 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.19 | 9.7 | 10.72 | 323146 | 341514 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7PR | LL207PR | ll20 7pr | ll207pr | Denbighshire | Sir Ddinbych | Llangollen WwTW | 598 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 323709 | 341865 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7PS | LL207PS | ll20 7ps | ll207ps | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1073 | 986 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.38 | 9.8 | 10.83 | 323921 | 341439 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7PT | LL207PT | ll20 7pt | ll207pt | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2002 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 324864 | 341006 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7PU | LL207PU | ll20 7pu | ll207pu | Wrexham | Wrecsam | Froncysyllte STW | 1150 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 326394 | 341060 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7PW | LL207PW | ll20 7pw | ll207pw | Denbighshire | Sir Ddinbych | Llangollen WwTW | 905 | 976 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.19 | 9.7 | 10.72 | 322748 | 341771 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7PY | LL207PY | ll20 7py | ll207py | Wrexham | Wrecsam | Cefn Mawr WwTW | 572 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327070 | 341273 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RA | LL207RA | ll20 7ra | ll207ra | Wrexham | Wrecsam | Cefn Mawr WwTW | 533 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327321 | 341183 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RB | LL207RB | ll20 7rb | ll207rb | Wrexham | Wrecsam | Cefn Mawr WwTW | 513 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327229 | 341237 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RD | LL207RD | ll20 7rd | ll207rd | Wrexham | Wrecsam | Cefn Mawr WwTW | 508 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327321 | 341209 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RE | LL207RE | ll20 7re | ll207re | Wrexham | Wrecsam | Cefn Mawr WwTW | 527 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327114 | 341294 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RF | LL207RF | ll20 7rf | ll207rf | Wrexham | Wrecsam | Cefn Mawr WwTW | 533 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327071 | 341325 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RG | LL207RG | ll20 7rg | ll207rg | Wrexham | Wrecsam | Cefn Mawr WwTW | 437 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327418 | 341264 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RH | LL207RH | ll20 7rh | ll207rh | Wrexham | Wrecsam | Cefn Mawr WwTW | 526 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 326993 | 341439 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RJ | LL207RJ | ll20 7rj | ll207rj | Wrexham | Wrecsam | Cefn Mawr WwTW | 581 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 326968 | 341376 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RL | LL207RL | ll20 7rl | ll207rl | Wrexham | Wrecsam | Cefn Mawr WwTW | 635 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327236 | 341102 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RN | LL207RN | ll20 7rn | ll207rn | Wrexham | Wrecsam | Cefn Mawr WwTW | 584 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327107 | 341228 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RP | LL207RP | ll20 7rp | ll207rp | Wrexham | Wrecsam | Cefn Mawr WwTW | 808 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 326820 | 341194 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RR | LL207RR | ll20 7rr | ll207rr | Wrexham | Wrecsam | Froncysyllte STW | 1199 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 326436 | 340969 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RS | LL207RS | ll20 7rs | ll207rs | Wrexham | Wrecsam | Cefn Mawr WwTW | 1073 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 326649 | 340987 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RT | LL207RT | ll20 7rt | ll207rt | Wrexham | Wrecsam | Cefn Mawr WwTW | 1123 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 326722 | 340846 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RU | LL207RU | ll20 7ru | ll207ru | Wrexham | Wrecsam | Cefn Mawr WwTW | 968 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327042 | 340822 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RW | LL207RW | ll20 7rw | ll207rw | Wrexham | Wrecsam | Cefn Mawr WwTW | 584 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327089 | 341241 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7RY | LL207RY | ll20 7ry | ll207ry | Wrexham | Wrecsam | Froncysyllte STW | 2115 | 1020 | 900to1200 | 2.04 | 1.49 | 1.1 | 19.01 | 10.14 | 11.21 | 325907 | 340221 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SA | LL207SA | ll20 7sa | ll207sa | Wrexham | Wrecsam | Cefn Mawr WwTW | 753 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327070 | 341050 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SB | LL207SB | ll20 7sb | ll207sb | Wrexham | Wrecsam | Cefn Mawr WwTW | 788 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327085 | 341002 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SD | LL207SD | ll20 7sd | ll207sd | Wrexham | Wrecsam | Cefn Mawr WwTW | 791 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327102 | 340990 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SE | LL207SE | ll20 7se | ll207se | Wrexham | Wrecsam | Cefn Mawr WwTW | 769 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327196 | 340974 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SF | LL207SF | ll20 7sf | ll207sf | Wrexham | Wrecsam | Cefn Mawr WwTW | 764 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 326941 | 341131 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SG | LL207SG | ll20 7sg | ll207sg | Wrexham | Wrecsam | Cefn Mawr WwTW | 764 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 326915 | 341155 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SH | LL207SH | ll20 7sh | ll207sh | Wrexham | Wrecsam | Cefn Mawr WwTW | 811 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 326876 | 341128 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SL | LL207SL | ll20 7sl | ll207sl | Wrexham | Wrecsam | Cefn Mawr WwTW | 719 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327034 | 341114 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SN | LL207SN | ll20 7sn | ll207sn | Wrexham | Wrecsam | Cefn Mawr WwTW | 632 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327110 | 341168 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SP | LL207SP | ll20 7sp | ll207sp | Wrexham | Wrecsam | Cefn Mawr WwTW | 678 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327132 | 341101 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SS | LL207SS | ll20 7ss | ll207ss | Wrexham | Wrecsam | Cefn Mawr WwTW | 626 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327182 | 341135 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7ST | LL207ST | ll20 7st | ll207st | Wrexham | Wrecsam | Cefn Mawr WwTW | 594 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327232 | 341148 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SU | LL207SU | ll20 7su | ll207su | Wrexham | Wrecsam | Cefn Mawr WwTW | 628 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327070 | 341200 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SW | LL207SW | ll20 7sw | ll207sw | Wrexham | Wrecsam | Cefn Mawr WwTW | 673 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327122 | 341113 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7SY | LL207SY | ll20 7sy | ll207sy | Wrexham | Wrecsam | Cefn Mawr WwTW | 745 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 327164 | 341012 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TA | LL207TA | ll20 7ta | ll207ta | Denbighshire | Sir Ddinbych | Froncysyllte STW | 774 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 326367 | 342177 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7TB | LL207TB | ll20 7tb | ll207tb | Wrexham | Wrecsam | Froncysyllte STW | 755 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 326501 | 342406 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TD | LL207TD | ll20 7td | ll207td | Wrexham | Wrecsam | Froncysyllte STW | 755 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 326448 | 342322 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TE | LL207TE | ll20 7te | ll207te | Wrexham | Wrecsam | Froncysyllte STW | 755 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 326469 | 342358 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TF | LL207TF | ll20 7tf | ll207tf | Wrexham | Wrecsam | Froncysyllte STW | 700 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 326658 | 342494 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TG | LL207TG | ll20 7tg | ll207tg | Wrexham | Wrecsam | Froncysyllte STW | 787 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 326424 | 342345 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TJ | LL207TJ | ll20 7tj | ll207tj | Wrexham | Wrecsam | Froncysyllte STW | 560 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 326925 | 342488 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TL | LL207TL | ll20 7tl | ll207tl | Wrexham | Wrecsam | Froncysyllte STW | 745 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 326849 | 342657 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TN | LL207TN | ll20 7tn | ll207tn | Wrexham | Wrecsam | Froncysyllte STW | 708 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 327027 | 342663 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TP | LL207TP | ll20 7tp | ll207tp | Wrexham | Wrecsam | Froncysyllte STW | 500 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 327071 | 342458 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TQ | LL207TQ | ll20 7tq | ll207tq | Wrexham | Wrecsam | Froncysyllte STW | 546 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 326997 | 342494 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TR | LL207TR | ll20 7tr | ll207tr | Wrexham | Wrecsam | Froncysyllte STW | 428 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 327090 | 342387 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TT | LL207TT | ll20 7tt | ll207tt | Wrexham | Wrecsam | Froncysyllte STW | 369 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 327143 | 342327 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TU | LL207TU | ll20 7tu | ll207tu | Wrexham | Wrecsam | Froncysyllte STW | 613 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 327080 | 342572 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TW | LL207TW | ll20 7tw | ll207tw | Wrexham | Wrecsam | Froncysyllte STW | 651 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 327036 | 342607 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TX | LL207TX | ll20 7tx | ll207tx | Wrexham | Wrecsam | Froncysyllte STW | 848 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 326491 | 342539 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7TY | LL207TY | ll20 7ty | ll207ty | Wrexham | Wrecsam | Froncysyllte STW | 220 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 327105 | 342180 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7UA | LL207UA | ll20 7ua | ll207ua | Wrexham | Wrecsam | Froncysyllte STW | 379 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 327033 | 342331 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7UB | LL207UB | ll20 7ub | ll207ub | Wrexham | Wrecsam | Froncysyllte STW | 530 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 326853 | 342423 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7UD | LL207UD | ll20 7ud | ll207ud | Wrexham | Wrecsam | Froncysyllte STW | 445 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 326844 | 342317 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7UE | LL207UE | ll20 7ue | ll207ue | Wrexham | Wrecsam | Froncysyllte STW | 491 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 326849 | 342376 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7UF | LL207UF | ll20 7uf | ll207uf | Wrexham | Wrecsam | Froncysyllte STW | 320 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 326989 | 342256 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7UH | LL207UH | ll20 7uh | ll207uh | Denbighshire | Sir Ddinbych | Llangollen WwTW | 331 | 1014 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.9 | 10.08 | 11.14 | 323679 | 342580 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7UL | LL207UL | ll20 7ul | ll207ul | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1690 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 325090 | 342178 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7UN | LL207UN | ll20 7un | ll207un | Denbighshire | Sir Ddinbych | Froncysyllte STW | 1602 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 325564 | 341542 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7UP | LL207UP | ll20 7up | ll207up | Wrexham | Wrecsam | Froncysyllte STW | 1410 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 325797 | 342474 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7UR | LL207UR | ll20 7ur | ll207ur | Wrexham | Wrecsam | Froncysyllte STW | 1227 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 326082 | 342629 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7US | LL207US | ll20 7us | ll207us | Wrexham | Wrecsam | Froncysyllte STW | 1170 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 326113 | 342571 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7UT | LL207UT | ll20 7ut | ll207ut | Wrexham | Wrecsam | Froncysyllte STW | 1173 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 326136 | 342613 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7UU | LL207UU | ll20 7uu | ll207uu | Wrexham | Wrecsam | Froncysyllte STW | 1015 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 326261 | 342515 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7UW | LL207UW | ll20 7uw | ll207uw | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1682 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 325000 | 341828 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7UY | LL207UY | ll20 7uy | ll207uy | Wrexham | Wrecsam | Froncysyllte STW | 1678 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 325717 | 342894 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YA | LL207YA | ll20 7ya | ll207ya | Wrexham | Wrecsam | Froncysyllte STW | 1818 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 325586 | 342951 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YB | LL207YB | ll20 7yb | ll207yb | Wrexham | Wrecsam | Froncysyllte STW | 1934 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 325512 | 343049 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YD | LL207YD | ll20 7yd | ll207yd | Wrexham | Wrecsam | Froncysyllte STW | 2032 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 325475 | 343165 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YE | LL207YE | ll20 7ye | ll207ye | Wrexham | Wrecsam | Froncysyllte STW | 1682 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 325726 | 342914 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YH | LL207YH | ll20 7yh | ll207yh | Wrexham | Wrecsam | Froncysyllte STW | 2177 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 325758 | 343665 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YL | LL207YL | ll20 7yl | ll207yl | Wrexham | Wrecsam | Llangollen WwTW | 1756 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 324991 | 343154 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YN | LL207YN | ll20 7yn | ll207yn | Wrexham | Wrecsam | Llangollen WwTW | 1931 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 325230 | 343036 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YP | LL207YP | ll20 7yp | ll207yp | Wrexham | Wrecsam | Froncysyllte STW | 1929 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 325436 | 342918 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YQ | LL207YQ | ll20 7yq | ll207yq | Wrexham | Wrecsam | Froncysyllte STW | 257 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 326995 | 342190 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YR | LL207YR | ll20 7yr | ll207yr | Wrexham | Wrecsam | Froncysyllte STW | 358 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 326812 | 342159 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YS | LL207YS | ll20 7ys | ll207ys | Wrexham | Wrecsam | Froncysyllte STW | 266 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 326900 | 342123 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YT | LL207YT | ll20 7yt | ll207yt | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 959 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 317847 | 344763 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7YU | LL207YU | ll20 7yu | ll207yu | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 586 | 987 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.4 | 9.81 | 10.84 | 318698 | 345100 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 7YW | LL207YW | ll20 7yw | ll207yw | Wrexham | Wrecsam | Froncysyllte STW | 2019 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 325422 | 343066 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL20 7YY | LL207YY | ll20 7yy | ll207yy | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 967 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 317813 | 344625 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AA | LL208AA | ll20 8aa | ll208aa | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2670 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 320745 | 342313 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AB | LL208AB | ll20 8ab | ll208ab | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2525 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 320898 | 342170 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AD | LL208AD | ll20 8ad | ll208ad | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2501 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 320913 | 342395 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AF | LL208AF | ll20 8af | ll208af | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2478 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 320936 | 342337 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AG | LL208AG | ll20 8ag | ll208ag | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2644 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 320736 | 342748 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AH | LL208AH | ll20 8ah | ll208ah | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2590 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 320836 | 342631 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AJ | LL208AJ | ll20 8aj | ll208aj | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 1242 | 1026 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.12 | 10.2 | 11.27 | 318600 | 343290 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AL | LL208AL | ll20 8al | ll208al | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2058 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 320418 | 343282 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AN | LL208AN | ll20 8an | ll208an | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 1810 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 319962 | 343154 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AP | LL208AP | ll20 8ap | ll208ap | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1962 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 321691 | 341446 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AQ | LL208AQ | ll20 8aq | ll208aq | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1947 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 321782 | 341322 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AR | LL208AR | ll20 8ar | ll208ar | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1528 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 322846 | 340966 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AS | LL208AS | ll20 8as | ll208as | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1744 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 321920 | 341483 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AT | LL208AT | ll20 8at | ll208at | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1702 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 322029 | 341394 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AU | LL208AU | ll20 8au | ll208au | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1791 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 321992 | 341295 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AW | LL208AW | ll20 8aw | ll208aw | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1821 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 321868 | 341422 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AX | LL208AX | ll20 8ax | ll208ax | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2303 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321111 | 342382 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AY | LL208AY | ll20 8ay | ll208ay | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1752 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 321972 | 341389 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8AZ | LL208AZ | ll20 8az | ll208az | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2530 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 320885 | 342455 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BA | LL208BA | ll20 8ba | ll208ba | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1579 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 322135 | 341457 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BB | LL208BB | ll20 8bb | ll208bb | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1613 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 322153 | 341377 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BD | LL208BD | ll20 8bd | ll208bd | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1509 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 322248 | 341425 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BE | LL208BE | ll20 8be | ll208be | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1821 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321721 | 341713 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BF | LL208BF | ll20 8bf | ll208bf | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2468 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 320948 | 342273 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BG | LL208BG | ll20 8bg | ll208bg | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1614 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321998 | 341608 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BH | LL208BH | ll20 8bh | ll208bh | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2265 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 320682 | 343300 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BJ | LL208BJ | ll20 8bj | ll208bj | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1548 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 322161 | 341474 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BL | LL208BL | ll20 8bl | ll208bl | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1578 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 322234 | 341336 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BN | LL208BN | ll20 8bn | ll208bn | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 1733 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 319789 | 343115 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BQ | LL208BQ | ll20 8bq | ll208bq | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1181 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 323074 | 341253 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BS | LL208BS | ll20 8bs | ll208bs | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 1565 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 319807 | 343344 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BT | LL208BT | ll20 8bt | ll208bt | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 894 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 319292 | 343791 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BU | LL208BU | ll20 8bu | ll208bu | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 234 | 987 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.4 | 9.81 | 10.84 | 319002 | 344573 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BW | LL208BW | ll20 8bw | ll208bw | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 1091 | 1026 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.12 | 10.2 | 11.27 | 318543 | 343453 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BX | LL208BX | ll20 8bx | ll208bx | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2172 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321377 | 341630 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BY | LL208BY | ll20 8by | ll208by | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 162 | 987 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.4 | 9.81 | 10.84 | 318934 | 344547 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8BZ | LL208BZ | ll20 8bz | ll208bz | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2140 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321406 | 341644 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DA | LL208DA | ll20 8da | ll208da | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 126 | 987 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.4 | 9.81 | 10.84 | 318884 | 344581 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DB | LL208DB | ll20 8db | ll208db | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 634 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 319404 | 344451 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DD | LL208DD | ll20 8dd | ll208dd | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 1543 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 320287 | 344218 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DE | LL208DE | ll20 8de | ll208de | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 1343 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 320116 | 344479 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DF | LL208DF | ll20 8df | ll208df | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 1364 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 320135 | 344441 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DG | LL208DG | ll20 8dg | ll208dg | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2608 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 319906 | 346868 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DH | LL208DH | ll20 8dh | ll208dh | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2501 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 319972 | 346713 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DN | LL208DN | ll20 8dn | ll208dn | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2518 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 319785 | 346824 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DP | LL208DP | ll20 8dp | ll208dp | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2282 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 318713 | 346799 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DR | LL208DR | ll20 8dr | ll208dr | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 3617 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 319289 | 348098 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DT | LL208DT | ll20 8dt | ll208dt | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 1739 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 320408 | 343926 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DU | LL208DU | ll20 8du | ll208du | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1526 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321898 | 342202 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DW | LL208DW | ll20 8dw | ll208dw | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 1272 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 319823 | 345238 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8DY | LL208DY | ll20 8dy | ll208dy | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1764 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 321685 | 342737 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8EB | LL208EB | ll20 8eb | ll208eb | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2552 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 321120 | 343503 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8ED | LL208ED | ll20 8ed | ll208ed | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2387 | 1048 | 900to1200 | 2.1 | 1.53 | 1.13 | 19.53 | 10.42 | 11.51 | 321709 | 344054 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8EE | LL208EE | ll20 8ee | ll208ee | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2010 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 320563 | 343605 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8EF | LL208EF | ll20 8ef | ll208ef | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2574 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 320949 | 343144 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8EG | LL208EG | ll20 8eg | ll208eg | Denbighshire | Sir Ddinbych | Llangollen WwTW | 739 | 1014 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.9 | 10.08 | 11.14 | 324124 | 342584 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8EH | LL208EH | ll20 8eh | ll208eh | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 3853 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 321969 | 346671 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8EJ | LL208EJ | ll20 8ej | ll208ej | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1962 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321609 | 341613 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8EL | LL208EL | ll20 8el | ll208el | Denbighshire | Sir Ddinbych | Llidiart Annie STW | 2230 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 320693 | 345654 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8EN | LL208EN | ll20 8en | ll208en | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1912 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321681 | 341575 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8EP | LL208EP | ll20 8ep | ll208ep | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2084 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321386 | 341903 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8EQ | LL208EQ | ll20 8eq | ll208eq | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1942 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321614 | 341654 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8ET | LL208ET | ll20 8et | ll208et | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1964 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321507 | 341914 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8EU | LL208EU | ll20 8eu | ll208eu | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1860 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321635 | 341840 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8EY | LL208EY | ll20 8ey | ll208ey | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1793 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321705 | 341839 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HA | LL208HA | ll20 8ha | ll208ha | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1882 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321617 | 341822 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HB | LL208HB | ll20 8hb | ll208hb | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1825 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321676 | 341827 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HD | LL208HD | ll20 8hd | ll208hd | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1801 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321712 | 341794 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HE | LL208HE | ll20 8he | ll208he | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1872 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321640 | 341786 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HF | LL208HF | ll20 8hf | ll208hf | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1946 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321567 | 341771 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HG | LL208HG | ll20 8hg | ll208hg | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2139 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321369 | 341757 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HH | LL208HH | ll20 8hh | ll208hh | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2138 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321341 | 341860 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HJ | LL208HJ | ll20 8hj | ll208hj | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1905 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321571 | 341902 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HL | LL208HL | ll20 8hl | ll208hl | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1873 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321598 | 341924 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HN | LL208HN | ll20 8hn | ll208hn | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1706 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321776 | 341904 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HS | LL208HS | ll20 8hs | ll208hs | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1691 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321808 | 341852 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HT | LL208HT | ll20 8ht | ll208ht | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1666 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321832 | 341861 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HU | LL208HU | ll20 8hu | ll208hu | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1784 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321689 | 341929 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HW | LL208HW | ll20 8hw | ll208hw | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1839 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321642 | 341892 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HY | LL208HY | ll20 8hy | ll208hy | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1711 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321761 | 341942 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8HZ | LL208HZ | ll20 8hz | ll208hz | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1628 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321844 | 341950 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LA | LL208LA | ll20 8la | ll208la | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1554 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321930 | 341923 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LB | LL208LB | ll20 8lb | ll208lb | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1467 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 322013 | 341948 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LD | LL208LD | ll20 8ld | ll208ld | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1276 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 322210 | 341961 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LF | LL208LF | ll20 8lf | ll208lf | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1446 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 322046 | 341915 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LG | LL208LG | ll20 8lg | ll208lg | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1429 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 322062 | 341920 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LH | LL208LH | ll20 8lh | ll208lh | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1610 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321887 | 341872 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LJ | LL208LJ | ll20 8lj | ll208lj | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1464 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 322028 | 341911 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LL | LL208LL | ll20 8ll | ll208ll | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1559 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321937 | 341885 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LN | LL208LN | ll20 8ln | ll208ln | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1151 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 322357 | 341927 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LP | LL208LP | ll20 8lp | ll208lp | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1470 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 322043 | 341853 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LR | LL208LR | ll20 8lr | ll208lr | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1530 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 322013 | 341768 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LS | LL208LS | ll20 8ls | ll208ls | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1609 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321918 | 341790 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LT | LL208LT | ll20 8lt | ll208lt | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1755 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321766 | 341780 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LU | LL208LU | ll20 8lu | ll208lu | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1543 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321976 | 341823 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8LW | LL208LW | ll20 8lw | ll208lw | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1261 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 322234 | 341938 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NA | LL208NA | ll20 8na | ll208na | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2192 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321258 | 341987 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NB | LL208NB | ll20 8nb | ll208nb | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2092 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321364 | 341964 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8ND | LL208ND | ll20 8nd | ll208nd | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1951 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321515 | 341936 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NE | LL208NE | ll20 8ne | ll208ne | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2088 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321375 | 341931 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NF | LL208NF | ll20 8nf | ll208nf | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1995 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321474 | 341917 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NN | LL208NN | ll20 8nn | ll208nn | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1912 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321549 | 341960 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NP | LL208NP | ll20 8np | ll208np | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1919 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321539 | 341972 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NQ | LL208NQ | ll20 8nq | ll208nq | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2173 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321285 | 341950 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NR | LL208NR | ll20 8nr | ll208nr | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1918 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321532 | 342010 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NS | LL208NS | ll20 8ns | ll208ns | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1928 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321526 | 341992 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NT | LL208NT | ll20 8nt | ll208nt | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1942 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321493 | 342096 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NU | LL208NU | ll20 8nu | ll208nu | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1963 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321480 | 342044 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NW | LL208NW | ll20 8nw | ll208nw | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1845 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321604 | 342025 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8NY | LL208NY | ll20 8ny | ll208ny | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1933 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321511 | 342044 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PB | LL208PB | ll20 8pb | ll208pb | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1927 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321513 | 342068 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PE | LL208PE | ll20 8pe | ll208pe | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1940 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321492 | 342118 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PF | LL208PF | ll20 8pf | ll208pf | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1860 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321583 | 342057 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PG | LL208PG | ll20 8pg | ll208pg | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1895 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321539 | 342110 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PL | LL208PL | ll20 8pl | ll208pl | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1837 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321614 | 342015 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PN | LL208PN | ll20 8pn | ll208pn | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1949 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321482 | 342126 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PP | LL208PP | ll20 8pp | ll208pp | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1991 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321451 | 342049 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PR | LL208PR | ll20 8pr | ll208pr | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2001 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321445 | 342028 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PS | LL208PS | ll20 8ps | ll208ps | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2025 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321421 | 342025 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PT | LL208PT | ll20 8pt | ll208pt | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2123 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321320 | 342033 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PU | LL208PU | ll20 8pu | ll208pu | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2124 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321322 | 342016 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PW | LL208PW | ll20 8pw | ll208pw | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1977 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321457 | 342103 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8PY | LL208PY | ll20 8py | ll208py | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2166 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321278 | 342022 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RA | LL208RA | ll20 8ra | ll208ra | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2228 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321214 | 342033 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RB | LL208RB | ll20 8rb | ll208rb | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2040 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321402 | 342043 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RD | LL208RD | ll20 8rd | ll208rd | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2119 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321321 | 342052 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RE | LL208RE | ll20 8re | ll208re | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2113 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321335 | 342004 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RF | LL208RF | ll20 8rf | ll208rf | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2132 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321320 | 341984 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RG | LL208RG | ll20 8rg | ll208rg | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2142 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321303 | 342019 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RH | LL208RH | ll20 8rh | ll208rh | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2199 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321265 | 341916 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RJ | LL208RJ | ll20 8rj | ll208rj | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1737 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321691 | 342158 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RN | LL208RN | ll20 8rn | ll208rn | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2196 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321249 | 342013 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RP | LL208RP | ll20 8rp | ll208rp | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1891 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321562 | 342001 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RQ | LL208RQ | ll20 8rq | ll208rq | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1700 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321747 | 342051 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RS | LL208RS | ll20 8rs | ll208rs | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2256 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321198 | 341961 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RT | LL208RT | ll20 8rt | ll208rt | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1976 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321480 | 341979 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RU | LL208RU | ll20 8ru | ll208ru | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1957 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321502 | 341966 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RW | LL208RW | ll20 8rw | ll208rw | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2098 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321366 | 341929 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RY | LL208RY | ll20 8ry | ll208ry | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1747 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321685 | 342132 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8RZ | LL208RZ | ll20 8rz | ll208rz | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1519 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321933 | 342046 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8SA | LL208SA | ll20 8sa | ll208sa | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1622 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321815 | 342107 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8SE | LL208SE | ll20 8se | ll208se | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1659 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321790 | 342042 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8SG | LL208SG | ll20 8sg | ll208sg | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1799 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321628 | 342165 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8SH | LL208SH | ll20 8sh | ll208sh | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1787 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321640 | 342167 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8SL | LL208SL | ll20 8sl | ll208sl | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2293 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321122 | 342322 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8SN | LL208SN | ll20 8sn | ll208sn | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2010 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321408 | 342253 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8SP | LL208SP | ll20 8sp | ll208sp | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2247 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321167 | 342355 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8SR | LL208SR | ll20 8sr | ll208sr | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2059 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321360 | 342233 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8SS | LL208SS | ll20 8ss | ll208ss | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2473 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 320968 | 342749 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8ST | LL208ST | ll20 8st | ll208st | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1923 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321496 | 342235 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8SU | LL208SU | ll20 8su | ll208su | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2264 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321150 | 342368 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8SW | LL208SW | ll20 8sw | ll208sw | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2117 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321297 | 342376 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8SY | LL208SY | ll20 8sy | ll208sy | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2339 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321075 | 342384 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8TA | LL208TA | ll20 8ta | ll208ta | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1930 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321487 | 342266 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8TB | LL208TB | ll20 8tb | ll208tb | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2062 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321360 | 342197 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8TD | LL208TD | ll20 8td | ll208td | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2097 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321324 | 342209 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8TE | LL208TE | ll20 8te | ll208te | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2429 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 321031 | 342856 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8TF | LL208TF | ll20 8tf | ll208tf | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2065 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 321352 | 342504 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8TG | LL208TG | ll20 8tg | ll208tg | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1918 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321496 | 342352 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8TH | LL208TH | ll20 8th | ll208th | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1775 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321647 | 342209 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8TJ | LL208TJ | ll20 8tj | ll208tj | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1972 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321447 | 342245 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8TP | LL208TP | ll20 8tp | ll208tp | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2202 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321214 | 342288 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8TY | LL208TY | ll20 8ty | ll208ty | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1789 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321706 | 341851 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 8UE | LL208UE | ll20 8ue | ll208ue | Denbighshire | Sir Ddinbych | Llangollen WwTW | 1830 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 321594 | 342193 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 9BA | LL209BA | ll20 9ba | ll209ba | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2098 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321366 | 341929 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 9BF | LL209BF | ll20 9bf | ll209bf | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2098 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321366 | 341929 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 9BG | LL209BG | ll20 9bg | ll209bg | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2098 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321366 | 341929 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL20 9BJ | LL209BJ | ll20 9bj | ll209bj | Denbighshire | Sir Ddinbych | Llangollen WwTW | 2098 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321366 | 341929 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AA | LL210AA | ll21 0aa | ll210aa | Denbighshire | Sir Ddinbych | Corwen WwTW | 455 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 307826 | 343505 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AB | LL210AB | ll21 0ab | ll210ab | Denbighshire | Sir Ddinbych | Corwen WwTW | 485 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307797 | 343498 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AD | LL210AD | ll21 0ad | ll210ad | Denbighshire | Sir Ddinbych | Corwen WwTW | 707 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 307570 | 343551 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AE | LL210AE | ll21 0ae | ll210ae | Denbighshire | Sir Ddinbych | Corwen WwTW | 729 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 307550 | 343513 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AG | LL210AG | ll21 0ag | ll210ag | Denbighshire | Sir Ddinbych | Corwen WwTW | 659 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307623 | 343484 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AH | LL210AH | ll21 0ah | ll210ah | Denbighshire | Sir Ddinbych | Corwen WwTW | 520 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307765 | 343478 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AJ | LL210AJ | ll21 0aj | ll210aj | Denbighshire | Sir Ddinbych | Cynwyd STW | 509 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305773 | 341256 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AL | LL210AL | ll21 0al | ll210al | Denbighshire | Sir Ddinbych | Corwen WwTW | 564 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307721 | 343476 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AN | LL210AN | ll21 0an | ll210an | Denbighshire | Sir Ddinbych | Corwen WwTW | 557 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 307723 | 343504 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AP | LL210AP | ll21 0ap | ll210ap | Denbighshire | Sir Ddinbych | Corwen WwTW | 607 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 307672 | 343510 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AR | LL210AR | ll21 0ar | ll210ar | Denbighshire | Sir Ddinbych | Corwen WwTW | 648 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 307632 | 343501 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AS | LL210AS | ll21 0as | ll210as | Denbighshire | Sir Ddinbych | Corwen WwTW | 694 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 307586 | 343503 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AT | LL210AT | ll21 0at | ll210at | Denbighshire | Sir Ddinbych | Corwen WwTW | 760 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 307519 | 343513 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AU | LL210AU | ll21 0au | ll210au | Denbighshire | Sir Ddinbych | Corwen WwTW | 477 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307822 | 343428 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0AY | LL210AY | ll21 0ay | ll210ay | Denbighshire | Sir Ddinbych | Corwen WwTW | 499 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307792 | 343453 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BA | LL210BA | ll21 0ba | ll210ba | Denbighshire | Sir Ddinbych | Corwen WwTW | 510 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307783 | 343442 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BB | LL210BB | ll21 0bb | ll210bb | Denbighshire | Sir Ddinbych | Corwen WwTW | 569 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307730 | 343415 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BD | LL210BD | ll21 0bd | ll210bd | Denbighshire | Sir Ddinbych | Corwen WwTW | 703 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307587 | 343435 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BE | LL210BE | ll21 0be | ll210be | Denbighshire | Sir Ddinbych | Corwen WwTW | 746 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307550 | 343404 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BG | LL210BG | ll21 0bg | ll210bg | Denbighshire | Sir Ddinbych | Corwen WwTW | 985 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307338 | 343272 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BH | LL210BH | ll21 0bh | ll210bh | Denbighshire | Sir Ddinbych | Corwen WwTW | 1095 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307219 | 343288 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BL | LL210BL | ll21 0bl | ll210bl | Denbighshire | Sir Ddinbych | Corwen WwTW | 948 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307534 | 342983 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BN | LL210BN | ll21 0bn | ll210bn | Denbighshire | Sir Ddinbych | Corwen WwTW | 691 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307614 | 343377 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BP | LL210BP | ll21 0bp | ll210bp | Denbighshire | Sir Ddinbych | Corwen WwTW | 1098 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307235 | 343224 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BS | LL210BS | ll21 0bs | ll210bs | Denbighshire | Sir Ddinbych | Corwen WwTW | 1128 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307219 | 343179 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BT | LL210BT | ll21 0bt | ll210bt | Denbighshire | Sir Ddinbych | Corwen WwTW | 1028 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307299 | 343253 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BU | LL210BU | ll21 0bu | ll210bu | Denbighshire | Sir Ddinbych | Corwen WwTW | 902 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307390 | 343404 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0BY | LL210BY | ll21 0by | ll210by | Denbighshire | Sir Ddinbych | Corwen WwTW | 1254 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307094 | 343155 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DA | LL210DA | ll21 0da | ll210da | Denbighshire | Sir Ddinbych | Corwen WwTW | 1308 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307047 | 343125 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DB | LL210DB | ll21 0db | ll210db | Denbighshire | Sir Ddinbych | Corwen WwTW | 268 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 308052 | 343426 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DD | LL210DD | ll21 0dd | ll210dd | Denbighshire | Sir Ddinbych | Corwen WwTW | 302 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307987 | 343484 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DE | LL210DE | ll21 0de | ll210de | Denbighshire | Sir Ddinbych | Corwen WwTW | 413 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307870 | 343497 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DF | LL210DF | ll21 0df | ll210df | Denbighshire | Sir Ddinbych | Corwen WwTW | 444 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307848 | 343455 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DG | LL210DG | ll21 0dg | ll210dg | Denbighshire | Sir Ddinbych | Corwen WwTW | 351 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307937 | 343481 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DJ | LL210DJ | ll21 0dj | ll210dj | Denbighshire | Sir Ddinbych | Corwen WwTW | 428 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 307848 | 343564 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DL | LL210DL | ll21 0dl | ll210dl | Denbighshire | Sir Ddinbych | Corwen WwTW | 377 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307918 | 343454 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DN | LL210DN | ll21 0dn | ll210dn | Denbighshire | Sir Ddinbych | Corwen WwTW | 379 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 307898 | 343546 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DP | LL210DP | ll21 0dp | ll210dp | Denbighshire | Sir Ddinbych | Corwen WwTW | 303 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 308021 | 343409 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DR | LL210DR | ll21 0dr | ll210dr | Denbighshire | Sir Ddinbych | Corwen WwTW | 249 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 308139 | 343365 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DT | LL210DT | ll21 0dt | ll210dt | Denbighshire | Sir Ddinbych | Corwen WwTW | 239 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 308123 | 343389 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DU | LL210DU | ll21 0du | ll210du | Denbighshire | Sir Ddinbych | Corwen WwTW | 231 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 308169 | 343368 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DW | LL210DW | ll21 0dw | ll210dw | Denbighshire | Sir Ddinbych | Corwen WwTW | 357 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307947 | 343434 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0DY | LL210DY | ll21 0dy | ll210dy | Denbighshire | Sir Ddinbych | Corwen WwTW | 198 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 308172 | 343404 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0EA | LL210EA | ll21 0ea | ll210ea | Denbighshire | Sir Ddinbych | Corwen WwTW | 266 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 308197 | 343319 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0EB | LL210EB | ll21 0eb | ll210eb | Denbighshire | Sir Ddinbych | Corwen WwTW | 281 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 308132 | 343332 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0ED | LL210ED | ll21 0ed | ll210ed | Denbighshire | Sir Ddinbych | Corwen WwTW | 240 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 308186 | 343351 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0EE | LL210EE | ll21 0ee | ll210ee | Denbighshire | Sir Ddinbych | Corwen WwTW | 1140 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307147 | 343418 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0EG | LL210EG | ll21 0eg | ll210eg | Denbighshire | Sir Ddinbych | Corwen WwTW | 1069 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307214 | 343455 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0EH | LL210EH | ll21 0eh | ll210eh | Denbighshire | Sir Ddinbych | Four Crosses STW | 2280 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305444 | 343721 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0EL | LL210EL | ll21 0el | ll210el | Denbighshire | Sir Ddinbych | Four Crosses STW | 1402 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 304439 | 343754 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0EN | LL210EN | ll21 0en | ll210en | Denbighshire | Sir Ddinbych | Four Crosses STW | 1512 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 303152 | 344431 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0EP | LL210EP | ll21 0ep | ll210ep | Denbighshire | Sir Ddinbych | Four Crosses STW | 489 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 303776 | 342790 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0ER | LL210ER | ll21 0er | ll210er | Denbighshire | Sir Ddinbych | Corwen WwTW | 1913 | 1039 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.37 | 10.33 | 11.42 | 306364 | 343592 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0ES | LL210ES | ll21 0es | ll210es | Denbighshire | Sir Ddinbych | Four Crosses STW | 1909 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305084 | 343623 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0ET | LL210ET | ll21 0et | ll210et | Denbighshire | Sir Ddinbych | Cynwyd STW | 1074 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 304257 | 340804 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0EU | LL210EU | ll21 0eu | ll210eu | Denbighshire | Sir Ddinbych | Cynwyd STW | 1153 | 1121 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.89 | 11.14 | 12.32 | 304240 | 341628 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0EW | LL210EW | ll21 0ew | ll210ew | Denbighshire | Sir Ddinbych | Cynwyd STW | 1335 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 305451 | 342454 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0HA | LL210HA | ll21 0ha | ll210ha | Gwynedd | Gwynedd | Glan Yr Afon STW | 163 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 302605 | 342566 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL21 0HB | LL210HB | ll21 0hb | ll210hb | Gwynedd | Gwynedd | Glan Yr Afon STW | 265 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 302302 | 342427 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL21 0HD | LL210HD | ll21 0hd | ll210hd | Gwynedd | Gwynedd | Glan Yr Afon STW | 667 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 301824 | 342439 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL21 0HE | LL210HE | ll21 0he | ll210he | Gwynedd | Gwynedd | Glan Yr Afon STW | 2550 | 1277 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.8 | 12.69 | 14.03 | 300042 | 341833 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL21 0HF | LL210HF | ll21 0hf | ll210hf | Gwynedd | Gwynedd | Glan Yr Afon STW | 1132 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 301862 | 341679 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL21 0HG | LL210HG | ll21 0hg | ll210hg | Gwynedd | Gwynedd | Glan Yr Afon STW | 231 | 1127 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.01 | 11.2 | 12.38 | 302229 | 342638 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL21 0HN | LL210HN | ll21 0hn | ll210hn | Denbighshire | Sir Ddinbych | Corwen WwTW | 1416 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 306957 | 343060 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0HP | LL210HP | ll21 0hp | ll210hp | Denbighshire | Sir Ddinbych | Cynwyd STW | 855 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 306042 | 341518 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0HR | LL210HR | ll21 0hr | ll210hr | Denbighshire | Sir Ddinbych | Cynwyd STW | 460 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305719 | 341268 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0HU | LL210HU | ll21 0hu | ll210hu | Denbighshire | Sir Ddinbych | Cynwyd STW | 325 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305600 | 341189 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0HW | LL210HW | ll21 0hw | ll210hw | Denbighshire | Sir Ddinbych | Cynwyd STW | 1742 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 306620 | 342243 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0HY | LL210HY | ll21 0hy | ll210hy | Denbighshire | Sir Ddinbych | Cynwyd STW | 197 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 305454 | 341223 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LA | LL210LA | ll21 0la | ll210la | Denbighshire | Sir Ddinbych | Cynwyd STW | 326 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305605 | 341150 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LB | LL210LB | ll21 0lb | ll210lb | Denbighshire | Sir Ddinbych | Cynwyd STW | 166 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 305445 | 341150 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LD | LL210LD | ll21 0ld | ll210ld | Denbighshire | Sir Ddinbych | Cynwyd STW | 365 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305641 | 341079 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LE | LL210LE | ll21 0le | ll210le | Denbighshire | Sir Ddinbych | Cynwyd STW | 412 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305690 | 341093 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LF | LL210LF | ll21 0lf | ll210lf | Denbighshire | Sir Ddinbych | Cynwyd STW | 430 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305704 | 341061 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LG | LL210LG | ll21 0lg | ll210lg | Denbighshire | Sir Ddinbych | Cynwyd STW | 565 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305842 | 341070 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LH | LL210LH | ll21 0lh | ll210lh | Denbighshire | Sir Ddinbych | Cynwyd STW | 594 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305836 | 340921 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LL | LL210LL | ll21 0ll | ll210ll | Denbighshire | Sir Ddinbych | Cynwyd STW | 534 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305795 | 340989 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LN | LL210LN | ll21 0ln | ll210ln | Denbighshire | Sir Ddinbych | Cynwyd STW | 2010 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 307203 | 340547 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LP | LL210LP | ll21 0lp | ll210lp | Denbighshire | Sir Ddinbych | Cynwyd STW | 441 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305696 | 340985 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LR | LL210LR | ll21 0lr | ll210lr | Denbighshire | Sir Ddinbych | Cynwyd STW | 414 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305671 | 340995 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LS | LL210LS | ll21 0ls | ll210ls | Denbighshire | Sir Ddinbych | Cynwyd STW | 412 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305682 | 341040 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LT | LL210LT | ll21 0lt | ll210lt | Denbighshire | Sir Ddinbych | Cynwyd STW | 386 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305604 | 340920 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LU | LL210LU | ll21 0lu | ll210lu | Denbighshire | Sir Ddinbych | Cynwyd STW | 383 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305586 | 340900 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LW | LL210LW | ll21 0lw | ll210lw | Denbighshire | Sir Ddinbych | Cynwyd STW | 468 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305729 | 340999 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0LY | LL210LY | ll21 0ly | ll210ly | Denbighshire | Sir Ddinbych | Cynwyd STW | 381 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 305489 | 340811 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0NA | LL210NA | ll21 0na | ll210na | Denbighshire | Sir Ddinbych | Cynwyd STW | 1303 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 304992 | 339860 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0NB | LL210NB | ll21 0nb | ll210nb | Denbighshire | Sir Ddinbych | Llandrillo STW | 1422 | 1104 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.58 | 10.97 | 12.13 | 304301 | 338687 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0ND | LL210ND | ll21 0nd | ll210nd | Denbighshire | Sir Ddinbych | Llandrillo STW | 1484 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 304876 | 338145 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0NE | LL210NE | ll21 0ne | ll210ne | Denbighshire | Sir Ddinbych | Llandrillo STW | 1778 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 304716 | 338822 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0NF | LL210NF | ll21 0nf | ll210nf | Denbighshire | Sir Ddinbych | Cynwyd STW | 968 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 305743 | 340280 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0NG | LL210NG | ll21 0ng | ll210ng | Denbighshire | Sir Ddinbych | Cynwyd STW | 469 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305744 | 341195 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0NH | LL210NH | ll21 0nh | ll210nh | Denbighshire | Sir Ddinbych | Cynwyd STW | 469 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305748 | 341096 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0NL | LL210NL | ll21 0nl | ll210nl | Denbighshire | Sir Ddinbych | Four Crosses STW | 881 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 304050 | 343400 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0NN | LL210NN | ll21 0nn | ll210nn | Denbighshire | Sir Ddinbych | Four Crosses STW | 315 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 303556 | 343120 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0NP | LL210NP | ll21 0np | ll210np | Gwynedd | Gwynedd | Glan Yr Afon STW | 1203 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 301873 | 343690 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL21 0NR | LL210NR | ll21 0nr | ll210nr | Conwy | Conwy | Dinmael STW | 1109 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 301776 | 344431 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0NS | LL210NS | ll21 0ns | ll210ns | Conwy | Conwy | Dinmael STW | 619 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 301318 | 344678 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0NT | LL210NT | ll21 0nt | ll210nt | Conwy | Conwy | Glan Yr Afon STW | 1451 | 1208 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.52 | 12.01 | 13.27 | 301115 | 343183 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0NU | LL210NU | ll21 0nu | ll210nu | Conwy | Conwy | Dinmael STW | 580 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 301266 | 344824 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0NW | LL210NW | ll21 0nw | ll210nw | Gwynedd | Gwynedd | Four Crosses STW | 538 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 302793 | 343087 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL21 0NX | LL210NX | ll21 0nx | ll210nx | Denbighshire | Sir Ddinbych | Cynwyd STW | 510 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 305789 | 341166 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0NY | LL210NY | ll21 0ny | ll210ny | Conwy | Conwy | Dinmael STW | 170 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 300534 | 344736 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0PA | LL210PA | ll21 0pa | ll210pa | Conwy | Conwy | Dinmael STW | 493 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 300538 | 345165 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0PB | LL210PB | ll21 0pb | ll210pb | Conwy | Conwy | Dinmael STW | 1242 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 299536 | 345132 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0PD | LL210PD | ll21 0pd | ll210pd | Conwy | Conwy | Dinmael STW | 924 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 300036 | 344058 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0PE | LL210PE | ll21 0pe | ll210pe | Conwy | Conwy | Dinmael STW | 1853 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 298880 | 344354 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0PF | LL210PF | ll21 0pf | ll210pf | Gwynedd | Gwynedd | Dinmael STW | 2207 | 1262 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.52 | 12.54 | 13.87 | 300035 | 342596 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL21 0PG | LL210PG | ll21 0pg | ll210pg | Gwynedd | Gwynedd | Sarnau STW | 3000 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 298558 | 341966 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL21 0PH | LL210PH | ll21 0ph | ll210ph | Gwynedd | Gwynedd | Sarnau STW | 1427 | 1433 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.71 | 14.24 | 15.74 | 297143 | 340766 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL21 0PL | LL210PL | ll21 0pl | ll210pl | Conwy | Conwy | Dinmael STW | 194 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 300531 | 344796 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0PN | LL210PN | ll21 0pn | ll210pn | Conwy | Conwy | Cerrigydrudion STW | 2734 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 296856 | 346059 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0PP | LL210PP | ll21 0pp | ll210pp | Conwy | Conwy | Dinmael STW | 519 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 300188 | 344618 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0PR | LL210PR | ll21 0pr | ll210pr | Conwy | Conwy | Dinmael STW | 1708 | 1220 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.74 | 12.13 | 13.4 | 298994 | 344777 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0PS | LL210PS | ll21 0ps | ll210ps | Conwy | Conwy | Dinmael STW | 1820 | 1220 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.74 | 12.13 | 13.4 | 298943 | 345172 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0PT | LL210PT | ll21 0pt | ll210pt | Conwy | Conwy | Dinmael STW | 2625 | 1266 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.6 | 12.58 | 13.91 | 298221 | 345561 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0PU | LL210PU | ll21 0pu | ll210pu | Conwy | Conwy | Cerrigydrudion STW | 2832 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 296985 | 346033 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0PY | LL210PY | ll21 0py | ll210py | Conwy | Conwy | Cerrigydrudion STW | 3535 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 296624 | 345018 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RA | LL210RA | ll21 0ra | ll210ra | Conwy | Conwy | Cerrigydrudion STW | 3848 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 296627 | 344682 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RB | LL210RB | ll21 0rb | ll210rb | Conwy | Conwy | Dinmael STW | 4383 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 296388 | 343921 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RD | LL210RD | ll21 0rd | ll210rd | Conwy | Conwy | Dinmael STW | 3771 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 296936 | 344491 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RE | LL210RE | ll21 0re | ll210re | Conwy | Conwy | Dinmael STW | 2252 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 298449 | 344738 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RF | LL210RF | ll21 0rf | ll210rf | Conwy | Conwy | Cerrigydrudion STW | 2640 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 296603 | 346006 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RG | LL210RG | ll21 0rg | ll210rg | Conwy | Conwy | Cerrigydrudion STW | 1851 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 296209 | 346690 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RH | LL210RH | ll21 0rh | ll210rh | Conwy | Conwy | Cerrigydrudion STW | 2571 | 1491 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.79 | 14.82 | 16.38 | 294960 | 345724 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RL | LL210RL | ll21 0rl | ll210rl | Conwy | Conwy | Cerrigydrudion STW | 3674 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 294368 | 344713 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RN | LL210RN | ll21 0rn | ll210rn | Gwynedd | Gwynedd | Cerrigydrudion STW | 4480 | 1578 | Over1500 | 3.16 | 2.31 | 1.69 | 29.41 | 15.69 | 17.34 | 292697 | 344603 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL21 0RP | LL210RP | ll21 0rp | ll210rp | Conwy | Conwy | Cerrigydrudion STW | 3965 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 296616 | 344553 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RR | LL210RR | ll21 0rr | ll210rr | Conwy | Conwy | Cerrigydrudion STW | 3811 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 296660 | 344734 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RS | LL210RS | ll21 0rs | ll210rs | Conwy | Conwy | Cerrigydrudion STW | 1220 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 295838 | 347204 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RT | LL210RT | ll21 0rt | ll210rt | Conwy | Conwy | Cerrigydrudion STW | 526 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295315 | 348800 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RU | LL210RU | ll21 0ru | ll210ru | Conwy | Conwy | Cefn Brith STW | 1056 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 294016 | 349437 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RW | LL210RW | ll21 0rw | ll210rw | Conwy | Conwy | Cerrigydrudion STW | 4059 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 295435 | 344223 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0RZ | LL210RZ | ll21 0rz | ll210rz | Denbighshire | Sir Ddinbych | Corwen WwTW | 206 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 308152 | 343408 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0SB | LL210SB | ll21 0sb | ll210sb | Conwy | Conwy | Cefn Brith STW | 4798 | 1728 | Over1500 | 3.46 | 2.53 | 1.86 | 32.21 | 17.18 | 18.99 | 289616 | 347205 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0SD | LL210SD | ll21 0sd | ll210sd | Conwy | Conwy | Cefn Brith STW | 4000 | 1711 | Over1500 | 3.42 | 2.51 | 1.84 | 31.89 | 17.01 | 18.8 | 290879 | 347080 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0SE | LL210SE | ll21 0se | ll210se | Conwy | Conwy | Cerrigydrudion STW | 2167 | 1550 | Over1500 | 3.1 | 2.27 | 1.66 | 28.89 | 15.41 | 17.03 | 293156 | 347751 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0SF | LL210SF | ll21 0sf | ll210sf | Conwy | Conwy | Cerrigydrudion STW | 761 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 294648 | 347822 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0SG | LL210SG | ll21 0sg | ll210sg | Conwy | Conwy | Cerrigydrudion STW | 2584 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 293460 | 346422 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0SJ | LL210SJ | ll21 0sj | ll210sj | Denbighshire | Sir Ddinbych | Llandrillo STW | 680 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303331 | 336836 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0SL | LL210SL | ll21 0sl | ll210sl | Denbighshire | Sir Ddinbych | Llandrillo STW | 675 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303290 | 336857 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0SN | LL210SN | ll21 0sn | ll210sn | Denbighshire | Sir Ddinbych | Llandrillo STW | 1025 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 304402 | 338049 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0SP | LL210SP | ll21 0sp | ll210sp | Denbighshire | Sir Ddinbych | Llandrillo STW | 367 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 303759 | 337179 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0SQ | LL210SQ | ll21 0sq | ll210sq | Denbighshire | Sir Ddinbych | Llandrillo STW | 382 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 303636 | 337108 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0SR | LL210SR | ll21 0sr | ll210sr | Denbighshire | Sir Ddinbych | Llandrillo STW | 248 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 303513 | 337235 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0SS | LL210SS | ll21 0ss | ll210ss | Denbighshire | Sir Ddinbych | Llandrillo STW | 461 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303478 | 337025 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0ST | LL210ST | ll21 0st | ll210st | Denbighshire | Sir Ddinbych | Llandrillo STW | 401 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303258 | 337205 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0SU | LL210SU | ll21 0su | ll210su | Denbighshire | Sir Ddinbych | Llandrillo STW | 570 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303358 | 336944 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0SW | LL210SW | ll21 0sw | ll210sw | Denbighshire | Sir Ddinbych | Llandrillo STW | 249 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 303664 | 337259 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0SY | LL210SY | ll21 0sy | ll210sy | Denbighshire | Sir Ddinbych | Llandrillo STW | 1865 | 1146 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.36 | 11.39 | 12.59 | 301845 | 336725 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TA | LL210TA | ll21 0ta | ll210ta | Denbighshire | Sir Ddinbych | Llandrillo STW | 1103 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 302576 | 337997 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TB | LL210TB | ll21 0tb | ll210tb | Denbighshire | Sir Ddinbych | Llandrillo STW | 1462 | 1206 | 1200to1500 | 2.41 | 1.77 | 1.3 | 22.48 | 11.99 | 13.25 | 302838 | 336204 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TD | LL210TD | ll21 0td | ll210td | Denbighshire | Sir Ddinbych | Llandrillo STW | 1317 | 1206 | 1200to1500 | 2.41 | 1.77 | 1.3 | 22.48 | 11.99 | 13.25 | 303343 | 336180 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TE | LL210TE | ll21 0te | ll210te | Denbighshire | Sir Ddinbych | Llandrillo STW | 3541 | 1317 | 1200to1500 | 2.64 | 1.93 | 1.41 | 24.55 | 13.09 | 14.47 | 302819 | 334016 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TF | LL210TF | ll21 0tf | ll210tf | Denbighshire | Sir Ddinbych | Llandrillo STW | 291 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 303618 | 337197 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TG | LL210TG | ll21 0tg | ll210tg | Denbighshire | Sir Ddinbych | Llandrillo STW | 349 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 303561 | 337131 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TH | LL210TH | ll21 0th | ll210th | Denbighshire | Sir Ddinbych | Llandrillo STW | 469 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 303543 | 337011 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TJ | LL210TJ | ll21 0tj | ll210tj | Denbighshire | Sir Ddinbych | Llandrillo STW | 391 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303374 | 337131 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TL | LL210TL | ll21 0tl | ll210tl | Denbighshire | Sir Ddinbych | Llandrillo STW | 404 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303414 | 337100 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TN | LL210TN | ll21 0tn | ll210tn | Denbighshire | Sir Ddinbych | Llandrillo STW | 309 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303456 | 337186 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TP | LL210TP | ll21 0tp | ll210tp | Denbighshire | Sir Ddinbych | Llandrillo STW | 459 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303298 | 337097 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TQ | LL210TQ | ll21 0tq | ll210tq | Denbighshire | Sir Ddinbych | Llandrillo STW | 308 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303419 | 337201 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TR | LL210TR | ll21 0tr | ll210tr | Denbighshire | Sir Ddinbych | Llandrillo STW | 752 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303264 | 336785 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TS | LL210TS | ll21 0ts | ll210ts | Conwy | Conwy | Cerrigydrudion STW | 3906 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 296711 | 344652 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 0TT | LL210TT | ll21 0tt | ll210tt | Denbighshire | Sir Ddinbych | Llandrillo STW | 596 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303264 | 336957 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TU | LL210TU | ll21 0tu | ll210tu | Denbighshire | Sir Ddinbych | Llandrillo STW | 222 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303468 | 337274 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0TW | LL210TW | ll21 0tw | ll210tw | Denbighshire | Sir Ddinbych | Llandrillo STW | 533 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 303322 | 336998 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 0UD | LL210UD | ll21 0ud | ll210ud | Denbighshire | Sir Ddinbych | Corwen WwTW | 735 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 307541 | 343557 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 1AQ | LL211AQ | ll21 1aq | ll211aq | Denbighshire | Sir Ddinbych | Corwen WwTW | 428 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 307848 | 343564 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AA | LL219AA | ll21 9aa | ll219aa | Denbighshire | Sir Ddinbych | Corwen WwTW | 1262 | 1035 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.29 | 10.29 | 11.37 | 308098 | 344822 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AB | LL219AB | ll21 9ab | ll219ab | Denbighshire | Sir Ddinbych | Corwen WwTW | 776 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 308004 | 344299 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AD | LL219AD | ll21 9ad | ll219ad | Denbighshire | Sir Ddinbych | Corwen WwTW | 710 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 308113 | 344264 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AE | LL219AE | ll21 9ae | ll219ae | Denbighshire | Sir Ddinbych | Corwen WwTW | 807 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 308071 | 344353 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AF | LL219AF | ll21 9af | ll219af | Denbighshire | Sir Ddinbych | Corwen WwTW | 774 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 308033 | 344308 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AG | LL219AG | ll21 9ag | ll219ag | Denbighshire | Sir Ddinbych | Carrog WwTW | 1162 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 310580 | 343641 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AH | LL219AH | ll21 9ah | ll219ah | Denbighshire | Sir Ddinbych | Carrog WwTW | 940 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 310808 | 343587 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AJ | LL219AJ | ll21 9aj | ll219aj | Denbighshire | Sir Ddinbych | Bryneglwys STW | 209 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 314449 | 347314 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AL | LL219AL | ll21 9al | ll219al | Denbighshire | Sir Ddinbych | Carrog WwTW | 987 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 310756 | 343631 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AN | LL219AN | ll21 9an | ll219an | Denbighshire | Sir Ddinbych | Carrog WwTW | 709 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 311032 | 343688 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AP | LL219AP | ll21 9ap | ll219ap | Denbighshire | Sir Ddinbych | Carrog WwTW | 624 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 311145 | 343521 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AR | LL219AR | ll21 9ar | ll219ar | Denbighshire | Sir Ddinbych | Carrog WwTW | 545 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 311224 | 343535 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AS | LL219AS | ll21 9as | ll219as | Denbighshire | Sir Ddinbych | Carrog WwTW | 495 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 311261 | 343585 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AT | LL219AT | ll21 9at | ll219at | Denbighshire | Sir Ddinbych | Carrog WwTW | 349 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 311391 | 343694 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AU | LL219AU | ll21 9au | ll219au | Denbighshire | Sir Ddinbych | Carrog WwTW | 285 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 311459 | 343758 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AW | LL219AW | ll21 9aw | ll219aw | Denbighshire | Sir Ddinbych | Carrog WwTW | 439 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 311302 | 343677 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9AY | LL219AY | ll21 9ay | ll219ay | Denbighshire | Sir Ddinbych | Carrog WwTW | 406 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 311355 | 343581 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BA | LL219BA | ll21 9ba | ll219ba | Denbighshire | Sir Ddinbych | Carrog WwTW | 432 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 311337 | 343554 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BB | LL219BB | ll21 9bb | ll219bb | Denbighshire | Sir Ddinbych | Carrog WwTW | 387 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 311366 | 343610 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BD | LL219BD | ll21 9bd | ll219bd | Denbighshire | Sir Ddinbych | Carrog WwTW | 141 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 311668 | 343589 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BE | LL219BE | ll21 9be | ll219be | Denbighshire | Sir Ddinbych | Carrog WwTW | 164 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 311590 | 343776 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BG | LL219BG | ll21 9bg | ll219bg | Denbighshire | Sir Ddinbych | Carrog WwTW | 815 | 1104 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.58 | 10.97 | 12.13 | 312547 | 343819 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BH | LL219BH | ll21 9bh | ll219bh | Denbighshire | Sir Ddinbych | Penrallt STW | 1281 | 1132 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.1 | 11.25 | 12.44 | 313258 | 343376 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BL | LL219BL | ll21 9bl | ll219bl | Denbighshire | Sir Ddinbych | Penrallt STW | 1108 | 1074 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.02 | 10.68 | 11.8 | 314120 | 343868 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BN | LL219BN | ll21 9bn | ll219bn | Denbighshire | Sir Ddinbych | Penrallt STW | 912 | 1059 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.74 | 10.53 | 11.64 | 314580 | 343690 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BP | LL219BP | ll21 9bp | ll219bp | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 443 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 315559 | 343286 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BS | LL219BS | ll21 9bs | ll219bs | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 1503 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 316427 | 343908 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BT | LL219BT | ll21 9bt | ll219bt | Denbighshire | Sir Ddinbych | Corwen WwTW | 1487 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 306892 | 344116 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BU | LL219BU | ll21 9bu | ll219bu | Denbighshire | Sir Ddinbych | Corwen WwTW | 1638 | 1035 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.29 | 10.29 | 11.37 | 307644 | 345084 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BW | LL219BW | ll21 9bw | ll219bw | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 417 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 314897 | 343136 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9BY | LL219BY | ll21 9by | ll219by | Denbighshire | Sir Ddinbych | Corwen WwTW | 2175 | 981 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.28 | 9.75 | 10.78 | 308949 | 345641 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DA | LL219DA | ll21 9da | ll219da | Denbighshire | Sir Ddinbych | Carrog WwTW | 2760 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 310518 | 346184 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DB | LL219DB | ll21 9db | ll219db | Denbighshire | Sir Ddinbych | Corwen WwTW | 2508 | 981 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.28 | 9.75 | 10.78 | 308917 | 345997 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DD | LL219DD | ll21 9dd | ll219dd | Denbighshire | Sir Ddinbych | Corwen WwTW | 2735 | 1035 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.29 | 10.29 | 11.37 | 306024 | 345124 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DE | LL219DE | ll21 9de | ll219de | Denbighshire | Sir Ddinbych | Corwen WwTW | 2674 | 1004 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.71 | 9.98 | 11.03 | 307488 | 346127 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DF | LL219DF | ll21 9df | ll219df | Denbighshire | Sir Ddinbych | Corwen WwTW | 3048 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 307507 | 346521 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DG | LL219DG | ll21 9dg | ll219dg | Denbighshire | Sir Ddinbych | Corwen WwTW | 3142 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 307446 | 346602 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DH | LL219DH | ll21 9dh | ll219dh | Denbighshire | Sir Ddinbych | Corwen WwTW | 3194 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 307528 | 346677 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DL | LL219DL | ll21 9dl | ll219dl | Denbighshire | Sir Ddinbych | Corwen WwTW | 3237 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 307641 | 346746 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DN | LL219DN | ll21 9dn | ll219dn | Denbighshire | Sir Ddinbych | Corwen WwTW | 3389 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 307628 | 346898 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DP | LL219DP | ll21 9dp | ll219dp | Denbighshire | Sir Ddinbych | Corwen WwTW | 3208 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 307570 | 346701 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DQ | LL219DQ | ll21 9dq | ll219dq | Denbighshire | Sir Ddinbych | Corwen WwTW | 3348 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 307632 | 346857 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DR | LL219DR | ll21 9dr | ll219dr | Denbighshire | Sir Ddinbych | Corwen WwTW | 3292 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 307604 | 346795 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DS | LL219DS | ll21 9ds | ll219ds | Denbighshire | Sir Ddinbych | Corwen WwTW | 3312 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 307555 | 346805 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DT | LL219DT | ll21 9dt | ll219dt | Denbighshire | Sir Ddinbych | Corwen WwTW | 3283 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 307567 | 346778 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DU | LL219DU | ll21 9du | ll219du | Denbighshire | Sir Ddinbych | Corwen WwTW | 3680 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 306693 | 346894 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9DW | LL219DW | ll21 9dw | ll219dw | Denbighshire | Sir Ddinbych | Corwen WwTW | 3119 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 307548 | 346605 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9EA | LL219EA | ll21 9ea | ll219ea | Denbighshire | Sir Ddinbych | Corwen WwTW | 4209 | 1014 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.9 | 10.08 | 11.14 | 308277 | 347781 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9ED | LL219ED | ll21 9ed | ll219ed | Denbighshire | Sir Ddinbych | Corwen WwTW | 3747 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 307893 | 347299 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9EE | LL219EE | ll21 9ee | ll219ee | Denbighshire | Sir Ddinbych | Corwen WwTW | 3226 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 308084 | 346792 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9EF | LL219EF | ll21 9ef | ll219ef | Denbighshire | Sir Ddinbych | Corwen WwTW | 455 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 308680 | 343363 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9EG | LL219EG | ll21 9eg | ll219eg | Denbighshire | Sir Ddinbych | Carrog WwTW | 1666 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 310135 | 343267 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9EH | LL219EH | ll21 9eh | ll219eh | Denbighshire | Sir Ddinbych | Carrog WwTW | 713 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 311319 | 343135 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9EJ | LL219EJ | ll21 9ej | ll219ej | Denbighshire | Sir Ddinbych | Corwen WwTW | 2675 | 1004 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.71 | 9.98 | 11.03 | 307407 | 346102 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9EL | LL219EL | ll21 9el | ll219el | Denbighshire | Sir Ddinbych | Carrog WwTW | 483 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 311907 | 343257 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9EN | LL219EN | ll21 9en | ll219en | Denbighshire | Sir Ddinbych | Carrog WwTW | 1733 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 310092 | 343174 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9EP | LL219EP | ll21 9ep | ll219ep | Denbighshire | Sir Ddinbych | Carrog WwTW | 383 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 311831 | 343338 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9ER | LL219ER | ll21 9er | ll219er | Denbighshire | Sir Ddinbych | Carrog WwTW | 399 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 311911 | 343350 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9ES | LL219ES | ll21 9es | ll219es | Denbighshire | Sir Ddinbych | Carrog WwTW | 427 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 311875 | 343305 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9ET | LL219ET | ll21 9et | ll219et | Denbighshire | Sir Ddinbych | Penrallt STW | 1464 | 1132 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.1 | 11.25 | 12.44 | 312938 | 342862 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9EU | LL219EU | ll21 9eu | ll219eu | Denbighshire | Sir Ddinbych | Penrallt STW | 268 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 314133 | 342813 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9EW | LL219EW | ll21 9ew | ll219ew | Denbighshire | Sir Ddinbych | Carrog WwTW | 413 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 311798 | 343301 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9EY | LL219EY | ll21 9ey | ll219ey | Denbighshire | Sir Ddinbych | Penrallt STW | 450 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 314828 | 342657 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HA | LL219HA | ll21 9ha | ll219ha | Denbighshire | Sir Ddinbych | Penrallt STW | 596 | 1138 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.21 | 11.31 | 12.5 | 314825 | 342378 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HB | LL219HB | ll21 9hb | ll219hb | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 373 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 314932 | 342792 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HD | LL219HD | ll21 9hd | ll219hd | Denbighshire | Sir Ddinbych | Penrallt STW | 55 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 314376 | 342747 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HE | LL219HE | ll21 9he | ll219he | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 454 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 314913 | 342670 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HF | LL219HF | ll21 9hf | ll219hf | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 303 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 314989 | 342837 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HG | LL219HG | ll21 9hg | ll219hg | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 560 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 314897 | 342533 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HH | LL219HH | ll21 9hh | ll219hh | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 444 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 315505 | 342574 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HL | LL219HL | ll21 9hl | ll219hl | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 525 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 315794 | 342918 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HN | LL219HN | ll21 9hn | ll219hn | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 819 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 315529 | 342173 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HP | LL219HP | ll21 9hp | ll219hp | Denbighshire | Sir Ddinbych | Penrallt STW | 587 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 314440 | 342211 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HR | LL219HR | ll21 9hr | ll219hr | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 381 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 314999 | 342682 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HS | LL219HS | ll21 9hs | ll219hs | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 340 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 315225 | 342613 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HT | LL219HT | ll21 9ht | ll219ht | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 362 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 315362 | 342600 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HU | LL219HU | ll21 9hu | ll219hu | Denbighshire | Sir Ddinbych | Corwen WwTW | 639 | 1040 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.38 | 10.34 | 11.43 | 308769 | 343980 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HW | LL219HW | ll21 9hw | ll219hw | Denbighshire | Sir Ddinbych | Glyndyfrdwy WwTW | 1483 | 1129 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.04 | 11.22 | 12.4 | 316613 | 342321 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9HY | LL219HY | ll21 9hy | ll219hy | Denbighshire | Sir Ddinbych | Corwen WwTW | 1637 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 309884 | 343877 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LA | LL219LA | ll21 9la | ll219la | Denbighshire | Sir Ddinbych | Carrog WwTW | 1404 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 310548 | 344452 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LB | LL219LB | ll21 9lb | ll219lb | Denbighshire | Sir Ddinbych | Carrog WwTW | 1091 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 310909 | 344416 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LD | LL219LD | ll21 9ld | ll219ld | Denbighshire | Sir Ddinbych | Carrog WwTW | 1507 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 311695 | 345216 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LE | LL219LE | ll21 9le | ll219le | Denbighshire | Sir Ddinbych | Bryneglwys STW | 1630 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 312896 | 346344 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LF | LL219LF | ll21 9lf | ll219lf | Denbighshire | Sir Ddinbych | Bryneglwys STW | 455 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 314391 | 346818 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LG | LL219LG | ll21 9lg | ll219lg | Denbighshire | Sir Ddinbych | Bryneglwys STW | 294 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 314411 | 347004 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LH | LL219LH | ll21 9lh | ll219lh | Denbighshire | Sir Ddinbych | Bryneglwys STW | 277 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 314520 | 347189 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LL | LL219LL | ll21 9ll | ll219ll | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 222 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 314542 | 347275 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LN | LL219LN | ll21 9ln | ll219ln | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 306 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 314647 | 347137 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LP | LL219LP | ll21 9lp | ll219lp | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 183 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 314864 | 347498 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LQ | LL219LQ | ll21 9lq | ll219lq | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 329 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 314562 | 347137 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LR | LL219LR | ll21 9lr | ll219lr | Denbighshire | Sir Ddinbych | Bryneglwys STW | 257 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 314461 | 347104 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LS | LL219LS | ll21 9ls | ll219ls | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 262 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 314555 | 347216 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LT | LL219LT | ll21 9lt | ll219lt | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 170 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 314860 | 347447 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LU | LL219LU | ll21 9lu | ll219lu | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 257 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 314925 | 347543 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LW | LL219LW | ll21 9lw | ll219lw | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 102 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 314733 | 347347 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9LY | LL219LY | ll21 9ly | ll219ly | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 196 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 314562 | 347588 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NA | LL219NA | ll21 9na | ll219na | Denbighshire | Sir Ddinbych | Bryneglwys STW | 772 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 313479 | 347272 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NB | LL219NB | ll21 9nb | ll219nb | Denbighshire | Sir Ddinbych | Bryneglwys STW | 2245 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 312010 | 347115 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9ND | LL219ND | ll21 9nd | ll219nd | Denbighshire | Sir Ddinbych | Bryneglwys STW | 499 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 314043 | 347704 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NE | LL219NE | ll21 9ne | ll219ne | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 826 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 315485 | 347215 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NF | LL219NF | ll21 9nf | ll219nf | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 437 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 314794 | 347864 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NG | LL219NG | ll21 9ng | ll219ng | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 550 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 315141 | 347755 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NH | LL219NH | ll21 9nh | ll219nh | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 1169 | 1002 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.68 | 9.96 | 11.01 | 315666 | 348082 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NL | LL219NL | ll21 9nl | ll219nl | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 2368 | 1020 | 900to1200 | 2.04 | 1.49 | 1.1 | 19.01 | 10.14 | 11.21 | 316707 | 348679 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NN | LL219NN | ll21 9nn | ll219nn | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 2571 | 1044 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.46 | 10.38 | 11.47 | 317177 | 348089 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NP | LL219NP | ll21 9np | ll219np | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 2370 | 1020 | 900to1200 | 2.04 | 1.49 | 1.1 | 19.01 | 10.14 | 11.21 | 316365 | 349115 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NS | LL219NS | ll21 9ns | ll219ns | Denbighshire | Sir Ddinbych | Four Crosses STW | 1920 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305115 | 343572 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NT | LL219NT | ll21 9nt | ll219nt | Denbighshire | Sir Ddinbych | Four Crosses STW | 1361 | 1103 | 900to1200 | 2.21 | 1.62 | 1.18 | 20.56 | 10.96 | 12.12 | 304552 | 343477 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NU | LL219NU | ll21 9nu | ll219nu | Denbighshire | Sir Ddinbych | Four Crosses STW | 935 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 304012 | 343540 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NW | LL219NW | ll21 9nw | ll219nw | Denbighshire | Sir Ddinbych | Min-Y-Rhos STW | 1396 | 1014 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.9 | 10.08 | 11.14 | 315164 | 348753 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9NY | LL219NY | ll21 9ny | ll219ny | Conwy | Conwy | Dinmael STW | 964 | 1030 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.2 | 10.24 | 11.32 | 301663 | 344739 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9PA | LL219PA | ll21 9pa | ll219pa | Conwy | Conwy | Dinmael STW | 1296 | 1174 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.88 | 11.67 | 12.9 | 300377 | 345955 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9PB | LL219PB | ll21 9pb | ll219pb | Conwy | Conwy | Dinmael STW | 1317 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 301671 | 345589 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9PD | LL219PD | ll21 9pd | ll219pd | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 768 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 302298 | 346112 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9PE | LL219PE | ll21 9pe | ll219pe | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 175 | 1052 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.61 | 10.46 | 11.56 | 302870 | 346352 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9PF | LL219PF | ll21 9pf | ll219pf | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 827 | 1117 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.82 | 11.1 | 12.27 | 302309 | 346697 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9PG | LL219PG | ll21 9pg | ll219pg | Conwy | Conwy | Betws Gwerfil Goch STW | 1728 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 301342 | 346628 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9PH | LL219PH | ll21 9ph | ll219ph | Conwy | Conwy | Betws Gwerfil Goch STW | 2468 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 300893 | 347526 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9PL | LL219PL | ll21 9pl | ll219pl | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 2279 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 301570 | 348051 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9PN | LL219PN | ll21 9pn | ll219pn | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 1003 | 1117 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.82 | 11.1 | 12.27 | 302413 | 347092 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9PP | LL219PP | ll21 9pp | ll219pp | Denbighshire | Sir Ddinbych | Llanfihangel Glyn Myfyr STW | 3124 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 302054 | 349886 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9PS | LL219PS | ll21 9ps | ll219ps | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 2046 | 1010 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.82 | 10.04 | 11.1 | 304474 | 344851 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9PT | LL219PT | ll21 9pt | ll219pt | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 356 | 1052 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.61 | 10.46 | 11.56 | 303357 | 346471 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9PU | LL219PU | ll21 9pu | ll219pu | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 290 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 303132 | 346585 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9PW | LL219PW | ll21 9pw | ll219pw | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 1855 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 301747 | 347639 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9PY | LL219PY | ll21 9py | ll219py | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 500 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 302993 | 346808 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9QX | LL219QX | ll21 9qx | ll219qx | Denbighshire | Sir Ddinbych | Corwen WwTW | 1240 | 1035 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.29 | 10.29 | 11.37 | 307590 | 344605 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9RA | LL219RA | ll21 9ra | ll219ra | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 644 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 303331 | 346884 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9RB | LL219RB | ll21 9rb | ll219rb | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 1522 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 304071 | 347429 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9RG | LL219RG | ll21 9rg | ll219rg | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 1937 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 302789 | 348230 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9RJ | LL219RJ | ll21 9rj | ll219rj | Denbighshire | Sir Ddinbych | Corwen WwTW | 1123 | 1035 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.29 | 10.29 | 11.37 | 307665 | 344515 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9RP | LL219RP | ll21 9rp | ll219rp | Denbighshire | Sir Ddinbych | Corwen WwTW | 1347 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 307142 | 344300 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9RR | LL219RR | ll21 9rr | ll219rr | Denbighshire | Sir Ddinbych | Corwen WwTW | 1351 | 1035 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.29 | 10.29 | 11.37 | 307528 | 344698 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9RS | LL219RS | ll21 9rs | ll219rs | Denbighshire | Sir Ddinbych | Corwen WwTW | 1349 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307429 | 344623 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9RT | LL219RT | ll21 9rt | ll219rt | Denbighshire | Sir Ddinbych | Corwen WwTW | 1257 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 307392 | 344466 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9RW | LL219RW | ll21 9rw | ll219rw | Denbighshire | Sir Ddinbych | Corwen WwTW | 635 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 308056 | 344168 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9RX | LL219RX | ll21 9rx | ll219rx | Denbighshire | Sir Ddinbych | Corwen WwTW | 1267 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 307301 | 344381 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9RZ | LL219RZ | ll21 9rz | ll219rz | Denbighshire | Sir Ddinbych | Corwen WwTW | 1460 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307452 | 344778 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9SE | LL219SE | ll21 9se | ll219se | Conwy | Conwy | Cerrigydrudion STW | 627 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295380 | 348892 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9SP | LL219SP | ll21 9sp | ll219sp | Conwy | Conwy | Cerrigydrudion STW | 479 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295367 | 348743 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9SR | LL219SR | ll21 9sr | ll219sr | Conwy | Conwy | Cerrigydrudion STW | 433 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295324 | 348705 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9SS | LL219SS | ll21 9ss | ll219ss | Conwy | Conwy | Cerrigydrudion STW | 381 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295325 | 348652 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9ST | LL219ST | ll21 9st | ll219st | Conwy | Conwy | Cerrigydrudion STW | 363 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295397 | 348612 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9SU | LL219SU | ll21 9su | ll219su | Conwy | Conwy | Cerrigydrudion STW | 277 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 295430 | 348494 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9SW | LL219SW | ll21 9sw | ll219sw | Conwy | Conwy | Cerrigydrudion STW | 573 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295400 | 348832 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9SY | LL219SY | ll21 9sy | ll219sy | Conwy | Conwy | Cerrigydrudion STW | 217 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 295272 | 348493 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TA | LL219TA | ll21 9ta | ll219ta | Conwy | Conwy | Cerrigydrudion STW | 261 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 295068 | 348456 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TB | LL219TB | ll21 9tb | ll219tb | Conwy | Conwy | Cerrigydrudion STW | 2289 | 1294 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.12 | 12.86 | 14.22 | 296582 | 350143 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TD | LL219TD | ll21 9td | ll219td | Conwy | Conwy | Cefn Brith STW | 1545 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 294797 | 349755 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TE | LL219TE | ll21 9te | ll219te | Conwy | Conwy | Cefn Brith STW | 1635 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 294840 | 350866 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TF | LL219TF | ll21 9tf | ll219tf | Conwy | Conwy | Cerrigydrudion STW | 476 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295397 | 348732 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TG | LL219TG | ll21 9tg | ll219tg | Conwy | Conwy | Cerrigydrudion STW | 367 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295285 | 348643 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TH | LL219TH | ll21 9th | ll219th | Conwy | Conwy | Cerrigydrudion STW | 318 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295356 | 348579 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TL | LL219TL | ll21 9tl | ll219tl | Conwy | Conwy | Cerrigydrudion STW | 353 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295410 | 348595 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TN | LL219TN | ll21 9tn | ll219tn | Conwy | Conwy | Cerrigydrudion STW | 312 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295415 | 348547 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TQ | LL219TQ | ll21 9tq | ll219tq | Conwy | Conwy | Cerrigydrudion STW | 384 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295468 | 348598 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TR | LL219TR | ll21 9tr | ll219tr | Conwy | Conwy | Cefn Brith STW | 335 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 293273 | 350570 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TS | LL219TS | ll21 9ts | ll219ts | Conwy | Conwy | Cefn Brith STW | 389 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 293217 | 350612 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TT | LL219TT | ll21 9tt | ll219tt | Conwy | Conwy | Alwen Septic Tank | 577 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 295797 | 353106 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TU | LL219TU | ll21 9tu | ll219tu | Conwy | Conwy | Pentre Llyn Cymer STW | 484 | 1283 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.91 | 12.75 | 14.1 | 297859 | 352784 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9TW | LL219TW | ll21 9tw | ll219tw | Conwy | Conwy | Cefn Brith STW | 207 | 1419 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.45 | 14.11 | 15.59 | 293458 | 350402 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9UA | LL219UA | ll21 9ua | ll219ua | Conwy | Conwy | Cerrigydrudion STW | 566 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295492 | 348792 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9UB | LL219UB | ll21 9ub | ll219ub | Conwy | Conwy | Cerrigydrudion STW | 702 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 295874 | 348614 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9UD | LL219UD | ll21 9ud | ll219ud | Conwy | Conwy | Cerrigydrudion STW | 591 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 295545 | 348793 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9UE | LL219UE | ll21 9ue | ll219ue | Conwy | Conwy | Cerrigydrudion STW | 499 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 295488 | 348720 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9UF | LL219UF | ll21 9uf | ll219uf | Conwy | Conwy | Llanfihangel Glyn Myfyr STW | 1770 | 1279 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.84 | 12.71 | 14.05 | 297196 | 349323 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9UG | LL219UG | ll21 9ug | ll219ug | Conwy | Conwy | Llanfihangel Glyn Myfyr STW | 394 | 1226 | 1200to1500 | 2.45 | 1.8 | 1.32 | 22.85 | 12.19 | 13.47 | 299141 | 349110 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9UH | LL219UH | ll21 9uh | ll219uh | Conwy | Conwy | Llanfihangel Glyn Myfyr STW | 1342 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 298290 | 348298 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9UL | LL219UL | ll21 9ul | ll219ul | Conwy | Conwy | Llanfihangel Glyn Myfyr STW | 991 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 299924 | 349230 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9UN | LL219UN | ll21 9un | ll219un | Conwy | Conwy | Llanfihangel Glyn Myfyr STW | 870 | 1235 | 1200to1500 | 2.47 | 1.81 | 1.33 | 23.02 | 12.28 | 13.57 | 298680 | 350283 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9UP | LL219UP | ll21 9up | ll219up | Denbighshire | Sir Ddinbych | Llanfihangel Glyn Myfyr STW | 1936 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 300878 | 349721 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9UR | LL219UR | ll21 9ur | ll219ur | Conwy | Conwy | Llanfihangel Glyn Myfyr STW | 374 | 1226 | 1200to1500 | 2.45 | 1.8 | 1.32 | 22.85 | 12.19 | 13.47 | 299044 | 349096 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9US | LL219US | ll21 9us | ll219us | Denbighshire | Sir Ddinbych | Betws Gwerfil Goch STW | 356 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 303167 | 346642 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9UW | LL219UW | ll21 9uw | ll219uw | Conwy | Conwy | Llanfihangel Glyn Myfyr STW | 1402 | 1275 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.76 | 12.67 | 14.01 | 299660 | 350674 | Conwy LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council
LL21 9YA | LL219YA | ll21 9ya | ll219ya | Denbighshire | Sir Ddinbych | Corwen WwTW | 1148 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 307423 | 344341 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9YB | LL219YB | ll21 9yb | ll219yb | Denbighshire | Sir Ddinbych | Corwen WwTW | 1376 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307310 | 344552 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9YD | LL219YD | ll21 9yd | ll219yd | Denbighshire | Sir Ddinbych | Corwen WwTW | 1335 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 307330 | 344514 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9YE | LL219YE | ll21 9ye | ll219ye | Denbighshire | Sir Ddinbych | Corwen WwTW | 1403 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 307122 | 344371 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL21 9YF | LL219YF | ll21 9yf | ll219yf | Denbighshire | Sir Ddinbych | Corwen WwTW | 1273 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 307362 | 344458 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL23 7AA | LL237AA | ll23 7aa | ll237aa | Gwynedd | Gwynedd | Bala WwTW | 1181 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292705 | 336034 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AB | LL237AB | ll23 7ab | ll237ab | Gwynedd | Gwynedd | Bala WwTW | 1216 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292655 | 336007 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AD | LL237AD | ll23 7ad | ll237ad | Gwynedd | Gwynedd | Bala WwTW | 1297 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292532 | 335894 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AE | LL237AE | ll23 7ae | ll237ae | Gwynedd | Gwynedd | Bala WwTW | 1311 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292526 | 335927 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AF | LL237AF | ll23 7af | ll237af | Gwynedd | Gwynedd | Bala WwTW | 1255 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292617 | 336017 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AG | LL237AG | ll23 7ag | ll237ag | Gwynedd | Gwynedd | Bala WwTW | 1192 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292729 | 336108 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AH | LL237AH | ll23 7ah | ll237ah | Gwynedd | Gwynedd | Bala WwTW | 1271 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292645 | 336119 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AJ | LL237AJ | ll23 7aj | ll237aj | Gwynedd | Gwynedd | Bala WwTW | 1312 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292536 | 335962 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AL | LL237AL | ll23 7al | ll237al | Gwynedd | Gwynedd | Bala WwTW | 1334 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292518 | 335975 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AN | LL237AN | ll23 7an | ll237an | Gwynedd | Gwynedd | Bala WwTW | 1402 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292461 | 336019 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AP | LL237AP | ll23 7ap | ll237ap | Gwynedd | Gwynedd | Bala WwTW | 1567 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292286 | 336017 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AQ | LL237AQ | ll23 7aq | ll237aq | Gwynedd | Gwynedd | Bala WwTW | 1742 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292064 | 335836 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AR | LL237AR | ll23 7ar | ll237ar | Gwynedd | Gwynedd | Bala WwTW | 1469 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292380 | 335989 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AS | LL237AS | ll23 7as | ll237as | Gwynedd | Gwynedd | Bala WwTW | 1499 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292336 | 335945 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AT | LL237AT | ll23 7at | ll237at | Gwynedd | Gwynedd | Bala WwTW | 1648 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292218 | 336068 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AU | LL237AU | ll23 7au | ll237au | Gwynedd | Gwynedd | Bala WwTW | 1072 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292794 | 335965 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AW | LL237AW | ll23 7aw | ll237aw | Gwynedd | Gwynedd | Bala WwTW | 1326 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292520 | 335958 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AX | LL237AX | ll23 7ax | ll237ax | Gwynedd | Gwynedd | Bala WwTW | 1521 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292553 | 336446 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7AY | LL237AY | ll23 7ay | ll237ay | Gwynedd | Gwynedd | Bala WwTW | 962 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292897 | 335927 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BA | LL237BA | ll23 7ba | ll237ba | Gwynedd | Gwynedd | Bala WwTW | 1052 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292836 | 336010 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BB | LL237BB | ll23 7bb | ll237bb | Gwynedd | Gwynedd | Bala WwTW | 1358 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292678 | 336341 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BD | LL237BD | ll23 7bd | ll237bd | Gwynedd | Gwynedd | Bala WwTW | 1510 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 292619 | 336513 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BE | LL237BE | ll23 7be | ll237be | Gwynedd | Gwynedd | Bala WwTW | 1301 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292753 | 336347 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BF | LL237BF | ll23 7bf | ll237bf | Gwynedd | Gwynedd | Bala WwTW | 919 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292882 | 335735 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BG | LL237BG | ll23 7bg | ll237bg | Gwynedd | Gwynedd | Bala WwTW | 1669 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292130 | 335785 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BH | LL237BH | ll23 7bh | ll237bh | Gwynedd | Gwynedd | Bala WwTW | 1271 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292570 | 335931 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BJ | LL237BJ | ll23 7bj | ll237bj | Gwynedd | Gwynedd | Bala WwTW | 947 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292848 | 335706 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BL | LL237BL | ll23 7bl | ll237bl | Gwynedd | Gwynedd | Bala WwTW | 1014 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292804 | 335817 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BN | LL237BN | ll23 7bn | ll237bn | Gwynedd | Gwynedd | Bala WwTW | 1003 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292795 | 335730 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BP | LL237BP | ll23 7bp | ll237bp | Gwynedd | Gwynedd | Bala WwTW | 920 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292865 | 335625 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BQ | LL237BQ | ll23 7bq | ll237bq | Gwynedd | Gwynedd | Bala WwTW | 1679 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292133 | 335864 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BS | LL237BS | ll23 7bs | ll237bs | Gwynedd | Gwynedd | Bala WwTW | 1371 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 292812 | 334582 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BT | LL237BT | ll23 7bt | ll237bt | Gwynedd | Gwynedd | Llangower STW | 1624 | 1604 | Over1500 | 3.21 | 2.35 | 1.72 | 29.9 | 15.94 | 17.62 | 291723 | 333335 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BU | LL237BU | ll23 7bu | ll237bu | Gwynedd | Gwynedd | Llangower STW | 1463 | 1769 | Over1500 | 3.54 | 2.59 | 1.9 | 32.97 | 17.58 | 19.44 | 291177 | 331077 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BW | LL237BW | ll23 7bw | ll237bw | Gwynedd | Gwynedd | Bala WwTW | 966 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292824 | 335676 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7BY | LL237BY | ll23 7by | ll237by | Gwynedd | Gwynedd | Llangower STW | 705 | 1634 | Over1500 | 3.27 | 2.39 | 1.75 | 30.46 | 16.24 | 17.95 | 290253 | 331660 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7DA | LL237DA | ll23 7da | ll237da | Gwynedd | Gwynedd | Llangower STW | 634 | 1634 | Over1500 | 3.27 | 2.39 | 1.75 | 30.46 | 16.24 | 17.95 | 290168 | 331768 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7DB | LL237DB | ll23 7db | ll237db | Gwynedd | Gwynedd | Llanuwchllyn STW | 999 | 1691 | Over1500 | 3.38 | 2.48 | 1.82 | 31.52 | 16.81 | 18.58 | 288991 | 330747 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7DD | LL237DD | ll23 7dd | ll237dd | Gwynedd | Gwynedd | Llanuwchllyn STW | 462 | 1774 | Over1500 | 3.55 | 2.6 | 1.91 | 33.06 | 17.63 | 19.49 | 288321 | 329895 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7DE | LL237DE | ll23 7de | ll237de | Gwynedd | Gwynedd | Llanuwchllyn STW | 1145 | 1892 | Over1500 | 3.79 | 2.77 | 2.03 | 35.26 | 18.81 | 20.79 | 288201 | 329160 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7DF | LL237DF | ll23 7df | ll237df | Gwynedd | Gwynedd | Llanuwchllyn STW | 3896 | 1814 | Over1500 | 3.63 | 2.66 | 1.95 | 33.81 | 18.03 | 19.93 | 289279 | 326588 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7DG | LL237DG | ll23 7dg | ll237dg | Gwynedd | Gwynedd | Bala WwTW | 1009 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292776 | 335623 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7DH | LL237DH | ll23 7dh | ll237dh | Gwynedd | Gwynedd | Bala WwTW | 1639 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 292533 | 336611 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7DN | LL237DN | ll23 7dn | ll237dn | Gwynedd | Gwynedd | Bala WwTW | 1083 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 293142 | 336424 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7DP | LL237DP | ll23 7dp | ll237dp | Gwynedd | Gwynedd | Llanfor STW | 874 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 295192 | 336756 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7DR | LL237DR | ll23 7dr | ll237dr | Gwynedd | Gwynedd | Llandderfel WwTW | 1876 | 1283 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.91 | 12.75 | 14.1 | 296581 | 336257 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7DS | LL237DS | ll23 7ds | ll237ds | Gwynedd | Gwynedd | Llanfor STW | 581 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 293784 | 336728 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7DT | LL237DT | ll23 7dt | ll237dt | Gwynedd | Gwynedd | Llanfor STW | 612 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 293746 | 336707 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7DU | LL237DU | ll23 7du | ll237du | Gwynedd | Gwynedd | Llanfor STW | 691 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 293709 | 336841 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7DW | LL237DW | ll23 7dw | ll237dw | Gwynedd | Gwynedd | Llanfor STW | 528 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 293815 | 336615 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7DX | LL237DX | ll23 7dx | ll237dx | Gwynedd | Gwynedd | Bala WwTW | 952 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292830 | 335555 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7DY | LL237DY | ll23 7dy | ll237dy | Gwynedd | Gwynedd | Llanfor STW | 1813 | 1420 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.47 | 14.12 | 15.6 | 293373 | 338093 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7DZ | LL237DZ | ll23 7dz | ll237dz | Gwynedd | Gwynedd | Bala WwTW | 969 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 292815 | 335489 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7EA | LL237EA | ll23 7ea | ll237ea | Gwynedd | Gwynedd | Frongoch STW | 2054 | 1433 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.71 | 14.24 | 15.74 | 292374 | 338157 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7EB | LL237EB | ll23 7eb | ll237eb | Gwynedd | Gwynedd | Frongoch STW | 2871 | 1707 | Over1500 | 3.42 | 2.5 | 1.83 | 31.82 | 16.97 | 18.75 | 291283 | 341898 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7ED | LL237ED | ll23 7ed | ll237ed | Gwynedd | Gwynedd | Frongoch STW | 4151 | 1758 | Over1500 | 3.52 | 2.57 | 1.89 | 32.77 | 17.48 | 19.31 | 290759 | 343265 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7EE | LL237EE | ll23 7ee | ll237ee | Gwynedd | Gwynedd | Frongoch STW | 3834 | 1714 | Over1500 | 3.43 | 2.51 | 1.84 | 31.95 | 17.04 | 18.83 | 291552 | 342822 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7EH | LL237EH | ll23 7eh | ll237eh | Gwynedd | Gwynedd | Bala WwTW | 1178 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292655 | 335894 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7EL | LL237EL | ll23 7el | ll237el | Gwynedd | Gwynedd | Bala WwTW | 1153 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292684 | 335901 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7EN | LL237EN | ll23 7en | ll237en | Gwynedd | Gwynedd | Bala WwTW | 1091 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292718 | 335793 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7EP | LL237EP | ll23 7ep | ll237ep | Gwynedd | Gwynedd | Llanfor STW | 750 | 1281 | 1200to1500 | 2.56 | 1.88 | 1.38 | 23.88 | 12.73 | 14.07 | 294849 | 336010 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7EQ | LL237EQ | ll23 7eq | ll237eq | Gwynedd | Gwynedd | Bala WwTW | 1066 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292764 | 335865 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7ER | LL237ER | ll23 7er | ll237er | Gwynedd | Gwynedd | Bala WwTW | 827 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 294413 | 335017 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7ES | LL237ES | ll23 7es | ll237es | Gwynedd | Gwynedd | Bala WwTW | 913 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 294277 | 334784 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7ET | LL237ET | ll23 7et | ll237et | Gwynedd | Gwynedd | Bala WwTW | 1324 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 294226 | 334304 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7EU | LL237EU | ll23 7eu | ll237eu | Gwynedd | Gwynedd | Bala WwTW | 1177 | 1273 | 1200to1500 | 2.55 | 1.86 | 1.37 | 23.73 | 12.65 | 13.99 | 294666 | 334775 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7EW | LL237EW | ll23 7ew | ll237ew | Gwynedd | Gwynedd | Bala WwTW | 1860 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 292694 | 334043 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7EY | LL237EY | ll23 7ey | ll237ey | Gwynedd | Gwynedd | Bala WwTW | 3795 | 1554 | Over1500 | 3.11 | 2.28 | 1.67 | 28.96 | 15.45 | 17.07 | 295883 | 332392 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7GA | LL237GA | ll23 7ga | ll237ga | Gwynedd | Gwynedd | Bala WwTW | 886 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292931 | 335798 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7HA | LL237HA | ll23 7ha | ll237ha | Gwynedd | Gwynedd | Bala WwTW | 759 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 293083 | 335846 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7HD | LL237HD | ll23 7hd | ll237hd | Gwynedd | Gwynedd | Llanfor STW | 1219 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 295193 | 337430 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HE | LL237HE | ll23 7he | ll237he | Gwynedd | Gwynedd | Sarnau STW | 1046 | 1348 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.12 | 13.4 | 14.81 | 296535 | 338467 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HF | LL237HF | ll23 7hf | ll237hf | Gwynedd | Gwynedd | Sarnau STW | 875 | 1402 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.13 | 13.94 | 15.4 | 296653 | 338594 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HG | LL237HG | ll23 7hg | ll237hg | Gwynedd | Gwynedd | Llandderfel WwTW | 384 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 298057 | 337285 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HH | LL237HH | ll23 7hh | ll237hh | Gwynedd | Gwynedd | Llandderfel WwTW | 178 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 298213 | 337145 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HL | LL237HL | ll23 7hl | ll237hl | Gwynedd | Gwynedd | Llandderfel WwTW | 98 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 298214 | 337028 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HN | LL237HN | ll23 7hn | ll237hn | Gwynedd | Gwynedd | Llandderfel WwTW | 90 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 298217 | 336983 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HP | LL237HP | ll23 7hp | ll237hp | Gwynedd | Gwynedd | Llandderfel WwTW | 114 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 298227 | 337075 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HQ | LL237HQ | ll23 7hq | ll237hq | Gwynedd | Gwynedd | Llandderfel WwTW | 207 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 298142 | 337120 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HR | LL237HR | ll23 7hr | ll237hr | Gwynedd | Gwynedd | Llandderfel WwTW | 71 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 298245 | 337029 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HS | LL237HS | ll23 7hs | ll237hs | Gwynedd | Gwynedd | Llandderfel WwTW | 61 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 298280 | 337048 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HT | LL237HT | ll23 7ht | ll237ht | Gwynedd | Gwynedd | Llandderfel WwTW | 126 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 298391 | 337086 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HU | LL237HU | ll23 7hu | ll237hu | Gwynedd | Gwynedd | Llandderfel WwTW | 278 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 298555 | 337116 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HW | LL237HW | ll23 7hw | ll237hw | Gwynedd | Gwynedd | Llandderfel WwTW | 123 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 298189 | 336955 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7HY | LL237HY | ll23 7hy | ll237hy | Gwynedd | Gwynedd | Llandderfel WwTW | 799 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 298372 | 337789 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7LA | LL237LA | ll23 7la | ll237la | Gwynedd | Gwynedd | Sarnau STW | 1589 | 1301 | 1200to1500 | 2.6 | 1.91 | 1.4 | 24.25 | 12.93 | 14.29 | 298698 | 339288 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7LB | LL237LB | ll23 7lb | ll237lb | Gwynedd | Gwynedd | Sarnau STW | 2137 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 299082 | 340163 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7LD | LL237LD | ll23 7ld | ll237ld | Gwynedd | Gwynedd | Sarnau STW | 2582 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 299587 | 340066 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7LE | LL237LE | ll23 7le | ll237le | Gwynedd | Gwynedd | Sarnau STW | 1630 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 298688 | 339745 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7LF | LL237LF | ll23 7lf | ll237lf | Gwynedd | Gwynedd | Sarnau STW | 611 | 1364 | 1200to1500 | 2.73 | 2 | 1.46 | 25.42 | 13.56 | 14.99 | 297693 | 339523 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7LG | LL237LG | ll23 7lg | ll237lg | Gwynedd | Gwynedd | Sarnau STW | 148 | 1402 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.13 | 13.94 | 15.4 | 297222 | 339437 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7LH | LL237LH | ll23 7lh | ll237lh | Gwynedd | Gwynedd | Sarnau STW | 336 | 1402 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.13 | 13.94 | 15.4 | 296775 | 339367 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7LL | LL237LL | ll23 7ll | ll237ll | Gwynedd | Gwynedd | Sarnau STW | 576 | 1402 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.13 | 13.94 | 15.4 | 296544 | 339234 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7LN | LL237LN | ll23 7ln | ll237ln | Gwynedd | Gwynedd | Sarnau STW | 1172 | 1453 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.08 | 14.44 | 15.96 | 295941 | 339416 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7LU | LL237LU | ll23 7lu | ll237lu | Gwynedd | Gwynedd | Bala WwTW | 1208 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292704 | 336095 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7LW | LL237LW | ll23 7lw | ll237lw | Gwynedd | Gwynedd | Sarnau STW | 2406 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 294719 | 339081 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7LY | LL237LY | ll23 7ly | ll237ly | Gwynedd | Gwynedd | Bala WwTW | 1173 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292740 | 336089 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7NA | LL237NA | ll23 7na | ll237na | Gwynedd | Gwynedd | Llanuwchllyn STW | 569 | 1774 | Over1500 | 3.55 | 2.6 | 1.91 | 33.06 | 17.63 | 19.49 | 287617 | 329997 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7ND | LL237ND | ll23 7nd | ll237nd | Gwynedd | Gwynedd | Bala WwTW | 1229 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292633 | 335987 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7NE | LL237NE | ll23 7ne | ll237ne | Gwynedd | Gwynedd | Bala WwTW | 1208 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292669 | 336021 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7NG | LL237NG | ll23 7ng | ll237ng | Gwynedd | Gwynedd | Bala WwTW | 1156 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292804 | 336167 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7NH | LL237NH | ll23 7nh | ll237nh | Gwynedd | Gwynedd | Bala WwTW | 1052 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292875 | 336084 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7NJ | LL237NJ | ll23 7nj | ll237nj | Gwynedd | Gwynedd | Bala WwTW | 680 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 293107 | 335633 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7NL | LL237NL | ll23 7nl | ll237nl | Gwynedd | Gwynedd | Bala WwTW | 811 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 293064 | 335928 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7NN | LL237NN | ll23 7nn | ll237nn | Gwynedd | Gwynedd | Bala WwTW | 1129 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292897 | 336252 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7NP | LL237NP | ll23 7np | ll237np | Gwynedd | Gwynedd | Llanfor STW | 1931 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 292536 | 337248 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7NR | LL237NR | ll23 7nr | ll237nr | Gwynedd | Gwynedd | Frongoch STW | 1042 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 291402 | 339734 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7NS | LL237NS | ll23 7ns | ll237ns | Gwynedd | Gwynedd | Frongoch STW | 527 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 290629 | 339642 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7NT | LL237NT | ll23 7nt | ll237nt | Gwynedd | Gwynedd | Frongoch STW | 356 | 1580 | Over1500 | 3.16 | 2.31 | 1.7 | 29.45 | 15.71 | 17.36 | 290253 | 339300 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7NU | LL237NU | ll23 7nu | ll237nu | Gwynedd | Gwynedd | Tryweryn Dam STW | 680 | 1741 | Over1500 | 3.48 | 2.55 | 1.87 | 32.45 | 17.31 | 19.13 | 288864 | 340279 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7NW | LL237NW | ll23 7nw | ll237nw | Gwynedd | Gwynedd | Bala WwTW | 1401 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 292840 | 336587 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7NY | LL237NY | ll23 7ny | ll237ny | Gwynedd | Gwynedd | Tryweryn Dam STW | 4412 | 2043 | Over1500 | 4.09 | 2.99 | 2.19 | 38.08 | 20.31 | 22.45 | 284266 | 341684 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7PA | LL237PA | ll23 7pa | ll237pa | Gwynedd | Gwynedd | Tryweryn Dam STW | 5887 | 2154 | Over1500 | 4.31 | 3.15 | 2.31 | 40.15 | 21.41 | 23.67 | 282416 | 339780 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7PB | LL237PB | ll23 7pb | ll237pb | Gwynedd | Gwynedd | Tryweryn Dam STW | 4237 | 2202 | Over1500 | 4.41 | 3.22 | 2.36 | 41.04 | 21.89 | 24.19 | 284084 | 339488 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7PH | LL237PH | ll23 7ph | ll237ph | Gwynedd | Gwynedd | Bala WwTW | 915 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 293027 | 335035 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7PL | LL237PL | ll23 7pl | ll237pl | Gwynedd | Gwynedd | Bala WwTW | 307 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 293955 | 335298 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7PN | LL237PN | ll23 7pn | ll237pn | Gwynedd | Gwynedd | Llanfor STW | 2016 | 1389 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.89 | 13.81 | 15.26 | 295937 | 335330 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7PP | LL237PP | ll23 7pp | ll237pp | Gwynedd | Gwynedd | Llanfor STW | 1676 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 295706 | 335589 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7PR | LL237PR | ll23 7pr | ll237pr | Gwynedd | Gwynedd | Llandderfel WwTW | 1885 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 297288 | 335407 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7PS | LL237PS | ll23 7ps | ll237ps | Gwynedd | Gwynedd | Llandderfel WwTW | 907 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 298255 | 336088 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7PT | LL237PT | ll23 7pt | ll237pt | Gwynedd | Gwynedd | Llandderfel WwTW | 668 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 298580 | 336384 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7PU | LL237PU | ll23 7pu | ll237pu | Gwynedd | Gwynedd | Llandderfel WwTW | 641 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 298552 | 336401 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7PW | LL237PW | ll23 7pw | ll237pw | Gwynedd | Gwynedd | Bala WwTW | 1924 | 1389 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.89 | 13.81 | 15.26 | 295547 | 334786 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7PY | LL237PY | ll23 7py | ll237py | Gwynedd | Gwynedd | Llandderfel WwTW | 1347 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 298798 | 335739 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7RA | LL237RA | ll23 7ra | ll237ra | Gwynedd | Gwynedd | Llandderfel WwTW | 1019 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 299168 | 336450 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7RB | LL237RB | ll23 7rb | ll237rb | Gwynedd | Gwynedd | Llandderfel WwTW | 500 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 298354 | 336495 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7RD | LL237RD | ll23 7rd | ll237rd | Gwynedd | Gwynedd | Llandderfel WwTW | 792 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 297844 | 336350 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7RE | LL237RE | ll23 7re | ll237re | Gwynedd | Gwynedd | Llandderfel WwTW | 871 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 299152 | 337199 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7RF | LL237RF | ll23 7rf | ll237rf | Gwynedd | Gwynedd | Llandderfel WwTW | 276 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 298482 | 337205 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7RG | LL237RG | ll23 7rg | ll237rg | Gwynedd | Gwynedd | Llandderfel WwTW | 1839 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 299958 | 337800 | Gwynedd LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council
LL23 7RH | LL237RH | ll23 7rh | ll237rh | Gwynedd | Gwynedd | Llandderfel WwTW | 2093 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 298372 | 334902 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7RL | LL237RL | ll23 7rl | ll237rl | Gwynedd | Gwynedd | Llandderfel WwTW | 2089 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 297774 | 334973 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7RN | LL237RN | ll23 7rn | ll237rn | Gwynedd | Gwynedd | Llandderfel WwTW | 2448 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 297125 | 334849 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7RR | LL237RR | ll23 7rr | ll237rr | Gwynedd | Gwynedd | Bala WwTW | 1186 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292664 | 335945 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7RS | LL237RS | ll23 7rs | ll237rs | Gwynedd | Gwynedd | Bala WwTW | 1145 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292740 | 336025 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7RT | LL237RT | ll23 7rt | ll237rt | Gwynedd | Gwynedd | Bala WwTW | 1195 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292758 | 336167 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7RU | LL237RU | ll23 7ru | ll237ru | Gwynedd | Gwynedd | Bala WwTW | 1289 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292712 | 336269 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7RY | LL237RY | ll23 7ry | ll237ry | Gwynedd | Gwynedd | Bala WwTW | 1632 | 1436 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.76 | 14.27 | 15.78 | 292463 | 336512 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SA | LL237SA | ll23 7sa | ll237sa | Gwynedd | Gwynedd | Rhyduchaf STW | 918 | 1505 | Over1500 | 3.01 | 2.2 | 1.62 | 28.05 | 14.96 | 16.54 | 291155 | 338105 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SB | LL237SB | ll23 7sb | ll237sb | Gwynedd | Gwynedd | Rhyduchaf STW | 801 | 1478 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.55 | 14.69 | 16.24 | 290542 | 337204 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SD | LL237SD | ll23 7sd | ll237sd | Gwynedd | Gwynedd | Rhyduchaf STW | 254 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 290003 | 337889 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SE | LL237SE | ll23 7se | ll237se | Gwynedd | Gwynedd | Tryweryn Dam STW | 1267 | 1663 | Over1500 | 3.33 | 2.44 | 1.79 | 31 | 16.53 | 18.27 | 288582 | 338665 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SF | LL237SF | ll23 7sf | ll237sf | Gwynedd | Gwynedd | Rhyduchaf STW | 1321 | 1665 | Over1500 | 3.33 | 2.44 | 1.79 | 31.03 | 16.55 | 18.29 | 288946 | 337744 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SG | LL237SG | ll23 7sg | ll237sg | Gwynedd | Gwynedd | Tryweryn Dam STW | 1888 | 1784 | Over1500 | 3.57 | 2.61 | 1.92 | 33.25 | 17.73 | 19.6 | 287526 | 338178 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SH | LL237SH | ll23 7sh | ll237sh | Gwynedd | Gwynedd | Rhyduchaf STW | 2893 | 1767 | Over1500 | 3.54 | 2.59 | 1.9 | 32.93 | 17.56 | 19.41 | 287599 | 336794 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SN | LL237SN | ll23 7sn | ll237sn | Gwynedd | Gwynedd | Bala WwTW | 1502 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292296 | 335764 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SP | LL237SP | ll23 7sp | ll237sp | Gwynedd | Gwynedd | Bala WwTW | 1328 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292478 | 335803 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SR | LL237SR | ll23 7sr | ll237sr | Gwynedd | Gwynedd | Bala WwTW | 1357 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292454 | 335830 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SS | LL237SS | ll23 7ss | ll237ss | Gwynedd | Gwynedd | Llangower STW | 1177 | 1665 | Over1500 | 3.33 | 2.44 | 1.79 | 31.03 | 16.55 | 18.29 | 289266 | 332413 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7ST | LL237ST | ll23 7st | ll237st | Gwynedd | Gwynedd | Llanuwchllyn STW | 1440 | 1672 | Over1500 | 3.35 | 2.45 | 1.8 | 31.16 | 16.62 | 18.37 | 288208 | 331735 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SU | LL237SU | ll23 7su | ll237su | Gwynedd | Gwynedd | Llanuwchllyn STW | 1975 | 1847 | Over1500 | 3.7 | 2.71 | 1.98 | 34.43 | 18.36 | 20.29 | 286523 | 331491 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SW | LL237SW | ll23 7sw | ll237sw | Gwynedd | Gwynedd | Bala WwTW | 1257 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292562 | 335853 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7SY | LL237SY | ll23 7sy | ll237sy | Gwynedd | Gwynedd | Llanuwchllyn STW | 2673 | 1952 | Over1500 | 3.91 | 2.86 | 2.1 | 36.38 | 19.4 | 21.45 | 285476 | 330816 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TA | LL237TA | ll23 7ta | ll237ta | Gwynedd | Gwynedd | Llanuwchllyn STW | 3293 | 1952 | Over1500 | 3.91 | 2.86 | 2.1 | 36.38 | 19.4 | 21.45 | 284854 | 330859 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TB | LL237TB | ll23 7tb | ll237tb | Gwynedd | Gwynedd | Llanuwchllyn STW | 2501 | 1863 | Over1500 | 3.73 | 2.73 | 2 | 34.72 | 18.52 | 20.47 | 285622 | 330650 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TD | LL237TD | ll23 7td | ll237td | Gwynedd | Gwynedd | Llanuwchllyn STW | 3480 | 1952 | Over1500 | 3.91 | 2.86 | 2.1 | 36.38 | 19.4 | 21.45 | 284906 | 331684 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TE | LL237TE | ll23 7te | ll237te | Gwynedd | Gwynedd | Parc STW | 5101 | 2123 | Over1500 | 4.25 | 3.11 | 2.28 | 39.57 | 21.1 | 23.33 | 282830 | 332503 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TF | LL237TF | ll23 7tf | ll237tf | Gwynedd | Gwynedd | Bala WwTW | 1230 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292570 | 335760 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TH | LL237TH | ll23 7th | ll237th | Gwynedd | Gwynedd | Llanuwchllyn STW | 835 | 1713 | Over1500 | 3.43 | 2.51 | 1.84 | 31.93 | 17.03 | 18.82 | 288348 | 331096 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TL | LL237TL | ll23 7tl | ll237tl | Gwynedd | Gwynedd | Llanuwchllyn STW | 508 | 1774 | Over1500 | 3.55 | 2.6 | 1.91 | 33.06 | 17.63 | 19.49 | 287918 | 329825 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TN | LL237TN | ll23 7tn | ll237tn | Gwynedd | Gwynedd | Llanuwchllyn STW | 454 | 1774 | Over1500 | 3.55 | 2.6 | 1.91 | 33.06 | 17.63 | 19.49 | 287862 | 329912 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TP | LL237TP | ll23 7tp | ll237tp | Gwynedd | Gwynedd | Llanuwchllyn STW | 503 | 1774 | Over1500 | 3.55 | 2.6 | 1.91 | 33.06 | 17.63 | 19.49 | 287796 | 329898 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TR | LL237TR | ll23 7tr | ll237tr | Gwynedd | Gwynedd | Llanuwchllyn STW | 572 | 1774 | Over1500 | 3.55 | 2.6 | 1.91 | 33.06 | 17.63 | 19.49 | 287742 | 329853 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TS | LL237TS | ll23 7ts | ll237ts | Gwynedd | Gwynedd | Llanuwchllyn STW | 487 | 1774 | Over1500 | 3.55 | 2.6 | 1.91 | 33.06 | 17.63 | 19.49 | 287773 | 329938 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TT | LL237TT | ll23 7tt | ll237tt | Gwynedd | Gwynedd | Llanuwchllyn STW | 536 | 1774 | Over1500 | 3.55 | 2.6 | 1.91 | 33.06 | 17.63 | 19.49 | 287690 | 329953 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TU | LL237TU | ll23 7tu | ll237tu | Gwynedd | Gwynedd | Llanuwchllyn STW | 486 | 1774 | Over1500 | 3.55 | 2.6 | 1.91 | 33.06 | 17.63 | 19.49 | 287730 | 329983 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TW | LL237TW | ll23 7tw | ll237tw | Gwynedd | Gwynedd | Llanuwchllyn STW | 351 | 1774 | Over1500 | 3.55 | 2.6 | 1.91 | 33.06 | 17.63 | 19.49 | 287857 | 330045 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7TY | LL237TY | ll23 7ty | ll237ty | Gwynedd | Gwynedd | Llanuwchllyn STW | 590 | 1774 | Over1500 | 3.55 | 2.6 | 1.91 | 33.06 | 17.63 | 19.49 | 287540 | 330110 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UA | LL237UA | ll23 7ua | ll237ua | Gwynedd | Gwynedd | Llanuwchllyn STW | 768 | 1840 | Over1500 | 3.68 | 2.69 | 1.98 | 34.29 | 18.29 | 20.22 | 287330 | 330306 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UB | LL237UB | ll23 7ub | ll237ub | Gwynedd | Gwynedd | Llanuwchllyn STW | 759 | 1840 | Over1500 | 3.68 | 2.69 | 1.98 | 34.29 | 18.29 | 20.22 | 287341 | 330347 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UD | LL237UD | ll23 7ud | ll237ud | Gwynedd | Gwynedd | Llanuwchllyn STW | 965 | 1847 | Over1500 | 3.7 | 2.71 | 1.98 | 34.43 | 18.36 | 20.29 | 287178 | 330590 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UE | LL237UE | ll23 7ue | ll237ue | Gwynedd | Gwynedd | Llanuwchllyn STW | 1407 | 1840 | Over1500 | 3.68 | 2.69 | 1.98 | 34.29 | 18.29 | 20.22 | 286918 | 329535 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UF | LL237UF | ll23 7uf | ll237uf | Gwynedd | Gwynedd | Llanuwchllyn STW | 2284 | 1946 | Over1500 | 3.89 | 2.85 | 2.09 | 36.27 | 19.34 | 21.38 | 285974 | 329463 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UG | LL237UG | ll23 7ug | ll237ug | Gwynedd | Gwynedd | Llanuwchllyn STW | 2835 | 2050 | Over1500 | 4.1 | 3 | 2.2 | 38.21 | 20.38 | 22.52 | 286158 | 328233 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UH | LL237UH | ll23 7uh | ll237uh | Gwynedd | Gwynedd | Llanuwchllyn STW | 3421 | 2050 | Over1500 | 4.1 | 3 | 2.2 | 38.21 | 20.38 | 22.52 | 285597 | 327967 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UN | LL237UN | ll23 7un | ll237un | Gwynedd | Gwynedd | Llanuwchllyn STW | 1570 | 1858 | Over1500 | 3.72 | 2.72 | 2 | 34.63 | 18.47 | 20.41 | 287276 | 328963 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UR | LL237UR | ll23 7ur | ll237ur | Gwynedd | Gwynedd | Bala WwTW | 1229 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292616 | 335938 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UT | LL237UT | ll23 7ut | ll237ut | Gwynedd | Gwynedd | Bala WwTW | 1288 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292581 | 336015 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UU | LL237UU | ll23 7uu | ll237uu | Gwynedd | Gwynedd | Bala WwTW | 1343 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292544 | 336071 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UW | LL237UW | ll23 7uw | ll237uw | Gwynedd | Gwynedd | Bala WwTW | 1764 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292245 | 336416 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7UY | LL237UY | ll23 7uy | ll237uy | Gwynedd | Gwynedd | Bala WwTW | 1350 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 292532 | 336059 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YA | LL237YA | ll23 7ya | ll237ya | Gwynedd | Gwynedd | Bala WwTW | 1617 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292399 | 336388 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YB | LL237YB | ll23 7yb | ll237yb | Gwynedd | Gwynedd | Bala WwTW | 1667 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292364 | 336426 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YD | LL237YD | ll23 7yd | ll237yd | Gwynedd | Gwynedd | Rhyduchaf STW | 2219 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 291510 | 336124 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YE | LL237YE | ll23 7ye | ll237ye | Gwynedd | Gwynedd | Bala WwTW | 1616 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292173 | 335694 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YF | LL237YF | ll23 7yf | ll237yf | Gwynedd | Gwynedd | Bala WwTW | 2447 | 1459 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.19 | 14.5 | 16.03 | 291405 | 334971 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YG | LL237YG | ll23 7yg | ll237yg | Gwynedd | Gwynedd | Rhyduchaf STW | 2667 | 1459 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.19 | 14.5 | 16.03 | 290680 | 335319 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YH | LL237YH | ll23 7yh | ll237yh | Gwynedd | Gwynedd | Llangower STW | 1272 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 290252 | 333598 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YL | LL237YL | ll23 7yl | ll237yl | Gwynedd | Gwynedd | Llangower STW | 1593 | 1665 | Over1500 | 3.33 | 2.44 | 1.79 | 31.03 | 16.55 | 18.29 | 288848 | 332364 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YN | LL237YN | ll23 7yn | ll237yn | Gwynedd | Gwynedd | Parc STW | 675 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 288156 | 333349 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YP | LL237YP | ll23 7yp | ll237yp | Gwynedd | Gwynedd | Parc STW | 111 | 1630 | Over1500 | 3.26 | 2.39 | 1.75 | 30.38 | 16.2 | 17.91 | 287630 | 333869 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YR | LL237YR | ll23 7yr | ll237yr | Gwynedd | Gwynedd | Parc STW | 87 | 1630 | Over1500 | 3.26 | 2.39 | 1.75 | 30.38 | 16.2 | 17.91 | 287734 | 333967 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YS | LL237YS | ll23 7ys | ll237ys | Gwynedd | Gwynedd | Parc STW | 2175 | 1952 | Over1500 | 3.91 | 2.86 | 2.1 | 36.38 | 19.4 | 21.45 | 286365 | 335564 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YT | LL237YT | ll23 7yt | ll237yt | Gwynedd | Gwynedd | Parc STW | 1120 | 1760 | Over1500 | 3.52 | 2.58 | 1.89 | 32.8 | 17.5 | 19.34 | 286690 | 334268 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YU | LL237YU | ll23 7yu | ll237yu | Gwynedd | Gwynedd | Parc STW | 949 | 1590 | Over1500 | 3.18 | 2.33 | 1.71 | 29.64 | 15.81 | 17.47 | 288592 | 334298 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YW | LL237YW | ll23 7yw | ll237yw | Gwynedd | Gwynedd | Parc STW | 129 | 1630 | Over1500 | 3.26 | 2.39 | 1.75 | 30.38 | 16.2 | 17.91 | 287652 | 333974 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YY | LL237YY | ll23 7yy | ll237yy | Gwynedd | Gwynedd | Bala WwTW | 1588 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292218 | 335824 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 7YZ | LL237YZ | ll23 7yz | ll237yz | Gwynedd | Gwynedd | Bala WwTW | 1698 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 292127 | 335928 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
LL23 9AF | LL239AF | ll23 9af | ll239af | Gwynedd | Gwynedd | Bala WwTW | 759 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 293083 | 335846 | Snowdonia National Park LPA | NW | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park
SY10 7NE | SY107NE | sy10 7ne | sy107ne | Wrexham | Wrecsam | Pontfadog STW | 1829 | 993 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.51 | 9.87 | 10.91 | 325708 | 337451 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY10 7NF | SY107NF | sy10 7nf | sy107nf | Wrexham | Wrecsam | Pontfadog STW | 1381 | 998 | 900to1200 | 2 | 1.46 | 1.07 | 18.6 | 9.92 | 10.96 | 325339 | 337706 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY10 7NS | SY107NS | sy10 7ns | sy107ns | Wrexham | Wrecsam | Dolywern STW | 3477 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 325120 | 335037 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY10 7NT | SY107NT | sy10 7nt | sy107nt | Wrexham | Wrecsam | Pontfadog STW | 2478 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 325299 | 336235 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY10 7NU | SY107NU | sy10 7nu | sy107nu | Wrexham | Wrecsam | Pontfadog STW | 2162 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 325102 | 336490 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY10 7NX | SY107NX | sy10 7nx | sy107nx | Wrexham | Wrecsam | Dolywern STW | 2659 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 324350 | 335402 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY10 7NY | SY107NY | sy10 7ny | sy107ny | Wrexham | Wrecsam | Dolywern STW | 2722 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 323648 | 334812 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY10 7NZ | SY107NZ | sy10 7nz | sy107nz | Wrexham | Wrecsam | Pandy STW | 1839 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 321005 | 334606 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2JH | SY132JH | sy13 2jh | sy132jh | Wrexham | Wrecsam | Bronington STW | 588 | 706 | 700to900 | 1.41 | 1.03 | 0.76 | 13.15 | 7.01 | 7.75 | 349227 | 340599 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2JJ | SY132JJ | sy13 2jj | sy132jj | Wrexham | Wrecsam | Bronington STW | 224 | 706 | 700to900 | 1.41 | 1.03 | 0.76 | 13.15 | 7.01 | 7.75 | 348849 | 340608 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2JN | SY132JN | sy13 2jn | sy132jn | Wrexham | Wrecsam | Bronington STW | 243 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 348453 | 340852 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2JP | SY132JP | sy13 2jp | sy132jp | Wrexham | Wrecsam | Bronington STW | 1044 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 347623 | 340893 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2JQ | SY132JQ | sy13 2jq | sy132jq | Wrexham | Wrecsam | Bronington STW | 689 | 706 | 700to900 | 1.41 | 1.03 | 0.76 | 13.15 | 7.01 | 7.75 | 349338 | 340741 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2JR | SY132JR | sy13 2jr | sy132jr | Wrexham | Wrecsam | Bronington STW | 1491 | 702 | 700to900 | 1.4 | 1.03 | 0.75 | 13.07 | 6.97 | 7.7 | 347172 | 340902 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2JS | SY132JS | sy13 2js | sy132js | Wrexham | Wrecsam | Bronington STW | 1873 | 702 | 700to900 | 1.4 | 1.03 | 0.75 | 13.07 | 6.97 | 7.7 | 346790 | 340920 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2JT | SY132JT | sy13 2jt | sy132jt | Wrexham | Wrecsam | Bronington STW | 1758 | 702 | 700to900 | 1.4 | 1.03 | 0.75 | 13.07 | 6.97 | 7.7 | 347080 | 341500 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2JU | SY132JU | sy13 2ju | sy132ju | Wrexham | Wrecsam | Bronington STW | 1554 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 347134 | 340370 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2JW | SY132JW | sy13 2jw | sy132jw | Wrexham | Wrecsam | Bronington STW | 754 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 347908 | 340842 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2JX | SY132JX | sy13 2jx | sy132jx | Wrexham | Wrecsam | Hanmer Arrowy STW | 1095 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 346096 | 337886 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2JZ | SY132JZ | sy13 2jz | sy132jz | Wrexham | Wrecsam | Hanmer Arrowy STW | 1410 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 346089 | 337571 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 2LQ | SY132LQ | sy13 2lq | sy132lq | Wrexham | Wrecsam | Hanmer Arrowy STW | 2048 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 344280 | 338104 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AD | SY133AD | sy13 3ad | sy133ad | Wrexham | Wrecsam | Fenns Bank STW | 2210 | 706 | 700to900 | 1.41 | 1.03 | 0.76 | 13.15 | 7.01 | 7.75 | 350876 | 341191 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AE | SY133AE | sy13 3ae | sy133ae | Wrexham | Wrecsam | Bronington STW | 1777 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 350399 | 341022 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AF | SY133AF | sy13 3af | sy133af | Wrexham | Wrecsam | Bronington STW | 2124 | 706 | 700to900 | 1.41 | 1.03 | 0.76 | 13.15 | 7.01 | 7.75 | 350706 | 341241 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AG | SY133AG | sy13 3ag | sy133ag | Wrexham | Wrecsam | Bronington STW | 1986 | 706 | 700to900 | 1.41 | 1.03 | 0.76 | 13.15 | 7.01 | 7.75 | 350508 | 341408 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AH | SY133AH | sy13 3ah | sy133ah | Wrexham | Wrecsam | Bronington STW | 1532 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 350169 | 340907 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AL | SY133AL | sy13 3al | sy133al | Wrexham | Wrecsam | Bronington STW | 1100 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 349658 | 341149 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AN | SY133AN | sy13 3an | sy133an | Wrexham | Wrecsam | Bronington STW | 1054 | 706 | 700to900 | 1.41 | 1.03 | 0.76 | 13.15 | 7.01 | 7.75 | 349462 | 341381 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AP | SY133AP | sy13 3ap | sy133ap | Wrexham | Wrecsam | Bronington STW | 1292 | 701 | 700to900 | 1.4 | 1.02 | 0.75 | 13.05 | 6.96 | 7.69 | 349466 | 341711 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AQ | SY133AQ | sy13 3aq | sy133aq | Wrexham | Wrecsam | Bronington STW | 1143 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 349770 | 340937 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AR | SY133AR | sy13 3ar | sy133ar | Wrexham | Wrecsam | Bronington STW | 1724 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 349897 | 341900 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AS | SY133AS | sy13 3as | sy133as | Wrexham | Wrecsam | Bronington STW | 2360 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 350413 | 342277 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AT | SY133AT | sy13 3at | sy133at | Wrexham | Wrecsam | Bronington STW | 2202 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 350452 | 341974 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AU | SY133AU | sy13 3au | sy133au | Wrexham | Wrecsam | Bronington STW | 2412 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 349595 | 342928 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AX | SY133AX | sy13 3ax | sy133ax | Wrexham | Wrecsam | Bronington STW | 2260 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 348207 | 342925 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AY | SY133AY | sy13 3ay | sy133ay | Wrexham | Wrecsam | Bronington STW | 2327 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 348243 | 343000 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3AZ | SY133AZ | sy13 3az | sy133az | Wrexham | Wrecsam | Bronington STW | 2450 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 347855 | 343026 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BA | SY133BA | sy13 3ba | sy133ba | Wrexham | Wrecsam | Bronington STW | 2682 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 347189 | 342958 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BB | SY133BB | sy13 3bb | sy133bb | Wrexham | Wrecsam | Bronington STW | 2978 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 346714 | 342972 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BD | SY133BD | sy13 3bd | sy133bd | Wrexham | Wrecsam | Bronington STW | 2387 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 346868 | 342297 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BE | SY133BE | sy13 3be | sy133be | Wrexham | Wrecsam | Bronington STW | 1868 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 347634 | 342277 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BG | SY133BG | sy13 3bg | sy133bg | Wrexham | Wrecsam | Bronington STW | 948 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 348120 | 341496 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BH | SY133BH | sy13 3bh | sy133bh | Wrexham | Wrecsam | Bronington STW | 1143 | 701 | 700to900 | 1.4 | 1.02 | 0.75 | 13.05 | 6.96 | 7.69 | 348751 | 341848 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BJ | SY133BJ | sy13 3bj | sy133bj | Wrexham | Wrecsam | Hanmer Arrowy STW | 818 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 345616 | 339616 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BQ | SY133BQ | sy13 3bq | sy133bq | Wrexham | Wrecsam | Bronington STW | 791 | 706 | 700to900 | 1.41 | 1.03 | 0.76 | 13.15 | 7.01 | 7.75 | 348746 | 341495 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BS | SY133BS | sy13 3bs | sy133bs | Wrexham | Wrecsam | Hanmer Arrowy STW | 1987 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 346352 | 340954 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BT | SY133BT | sy13 3bt | sy133bt | Wrexham | Wrecsam | Hanmer Arrowy STW | 2546 | 694 | 600to700 | 1.39 | 1.01 | 0.74 | 12.92 | 6.89 | 7.61 | 345794 | 341503 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BU | SY133BU | sy13 3bu | sy133bu | Wrexham | Wrecsam | Hanmer Arrowy STW | 2713 | 694 | 600to700 | 1.39 | 1.01 | 0.74 | 12.92 | 6.89 | 7.61 | 345661 | 341651 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BX | SY133BX | sy13 3bx | sy133bx | Wrexham | Wrecsam | Bronington STW | 3224 | 694 | 600to700 | 1.39 | 1.01 | 0.74 | 12.92 | 6.89 | 7.61 | 345857 | 342319 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BY | SY133BY | sy13 3by | sy133by | Wrexham | Wrecsam | Hanmer Arrowy STW | 2615 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 345470 | 341509 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3BZ | SY133BZ | sy13 3bz | sy133bz | Wrexham | Wrecsam | Hanmer Arrowy STW | 2561 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 345173 | 341354 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DA | SY133DA | sy13 3da | sy133da | Wrexham | Wrecsam | Hanmer Arrowy STW | 2423 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 345625 | 341349 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DB | SY133DB | sy13 3db | sy133db | Wrexham | Wrecsam | Hanmer Arrowy STW | 2134 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 345740 | 341077 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DD | SY133DD | sy13 3dd | sy133dd | Wrexham | Wrecsam | Hanmer Arrowy STW | 1719 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 345745 | 340655 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DE | SY133DE | sy13 3de | sy133de | Wrexham | Wrecsam | Hanmer Arrowy STW | 1011 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 345494 | 339765 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DF | SY133DF | sy13 3df | sy133df | Wrexham | Wrecsam | Hanmer Arrowy STW | 800 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 345530 | 339509 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DG | SY133DG | sy13 3dg | sy133dg | Wrexham | Wrecsam | Hanmer Arrowy STW | 1065 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 345417 | 339770 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DH | SY133DH | sy13 3dh | sy133dh | Wrexham | Wrecsam | Hanmer Arrowy STW | 1851 | 702 | 700to900 | 1.4 | 1.03 | 0.75 | 13.07 | 6.97 | 7.7 | 344340 | 339448 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DJ | SY133DJ | sy13 3dj | sy133dj | Wrexham | Wrecsam | Hanmer Arrowy STW | 1386 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 344802 | 339375 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DL | SY133DL | sy13 3dl | sy133dl | Wrexham | Wrecsam | Hanmer Arrowy STW | 2010 | 702 | 700to900 | 1.4 | 1.03 | 0.75 | 13.07 | 6.97 | 7.7 | 344122 | 338914 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DN | SY133DN | sy13 3dn | sy133dn | Wrexham | Wrecsam | Hanmer Arrowy STW | 1665 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 344518 | 339396 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DP | SY133DP | sy13 3dp | sy133dp | Wrexham | Wrecsam | Hanmer Arrowy STW | 2047 | 694 | 600to700 | 1.39 | 1.01 | 0.74 | 12.92 | 6.89 | 7.61 | 344425 | 340111 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DQ | SY133DQ | sy13 3dq | sy133dq | Wrexham | Wrecsam | Hanmer Arrowy STW | 1465 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 344713 | 339348 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DR | SY133DR | sy13 3dr | sy133dr | Wrexham | Wrecsam | Penley STW | 2423 | 702 | 700to900 | 1.4 | 1.03 | 0.75 | 13.07 | 6.97 | 7.7 | 343553 | 339208 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DS | SY133DS | sy13 3ds | sy133ds | Wrexham | Wrecsam | Penley STW | 1569 | 678 | 600to700 | 1.35 | 0.99 | 0.73 | 12.61 | 6.72 | 7.43 | 342949 | 341010 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DT | SY133DT | sy13 3dt | sy133dt | Wrexham | Wrecsam | Penley STW | 1989 | 675 | 600to700 | 1.35 | 0.99 | 0.72 | 12.55 | 6.69 | 7.4 | 343088 | 341629 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DU | SY133DU | sy13 3du | sy133du | Wrexham | Wrecsam | Penley STW | 2174 | 687 | 600to700 | 1.37 | 1 | 0.74 | 12.78 | 6.82 | 7.53 | 343520 | 341209 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DW | SY133DW | sy13 3dw | sy133dw | Wrexham | Wrecsam | Hanmer Arrowy STW | 1903 | 694 | 600to700 | 1.39 | 1.01 | 0.74 | 12.92 | 6.89 | 7.61 | 344315 | 339549 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DX | SY133DX | sy13 3dx | sy133dx | Wrexham | Wrecsam | Penley STW | 2284 | 687 | 600to700 | 1.37 | 1 | 0.74 | 12.78 | 6.82 | 7.53 | 343727 | 340864 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DY | SY133DY | sy13 3dy | sy133dy | Wrexham | Wrecsam | Hanmer Arrowy STW | 2693 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 344519 | 341137 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3DZ | SY133DZ | sy13 3dz | sy133dz | Wrexham | Wrecsam | Hanmer Arrowy STW | 2739 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 344650 | 341283 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EA | SY133EA | sy13 3ea | sy133ea | Wrexham | Wrecsam | Hanmer Arrowy STW | 2493 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 344794 | 341084 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EB | SY133EB | sy13 3eb | sy133eb | Wrexham | Wrecsam | Hanmer Arrowy STW | 2574 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 344746 | 341149 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3ED | SY133ED | sy13 3ed | sy133ed | Wrexham | Wrecsam | Hanmer Arrowy STW | 2471 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 344805 | 341065 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EE | SY133EE | sy13 3ee | sy133ee | Wrexham | Wrecsam | Hanmer Arrowy STW | 2363 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 344885 | 340987 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EG | SY133EG | sy13 3eg | sy133eg | Wrexham | Wrecsam | Hanmer Arrowy STW | 974 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 346586 | 339840 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EH | SY133EH | sy13 3eh | sy133eh | Wrexham | Wrecsam | Hanmer Arrowy STW | 548 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 346341 | 338474 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EJ | SY133EJ | sy13 3ej | sy133ej | Wrexham | Wrecsam | Hanmer Arrowy STW | 712 | 718 | 700to900 | 1.44 | 1.05 | 0.77 | 13.37 | 7.13 | 7.88 | 345510 | 338630 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EL | SY133EL | sy13 3el | sy133el | Wrexham | Wrecsam | Hanmer Arrowy STW | 395 | 718 | 700to900 | 1.44 | 1.05 | 0.77 | 13.37 | 7.13 | 7.88 | 345797 | 339193 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EN | SY133EN | sy13 3en | sy133en | Wrexham | Wrecsam | Hanmer Arrowy STW | 1595 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 346224 | 340572 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EP | SY133EP | sy13 3ep | sy133ep | Wrexham | Wrecsam | Bronington STW | 1329 | 718 | 700to900 | 1.44 | 1.05 | 0.77 | 13.37 | 7.13 | 7.88 | 348764 | 339386 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EQ | SY133EQ | sy13 3eq | sy133eq | Wrexham | Wrecsam | Hanmer Arrowy STW | 275 | 718 | 700to900 | 1.44 | 1.05 | 0.77 | 13.37 | 7.13 | 7.88 | 346042 | 339240 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3ER | SY133ER | sy13 3er | sy133er | Wrexham | Wrecsam | Bronington STW | 1257 | 718 | 700to900 | 1.44 | 1.05 | 0.77 | 13.37 | 7.13 | 7.88 | 348922 | 339483 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3ET | SY133ET | sy13 3et | sy133et | Wrexham | Wrecsam | Fenns Bank STW | 1928 | 706 | 700to900 | 1.41 | 1.03 | 0.76 | 13.15 | 7.01 | 7.75 | 350853 | 340900 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EU | SY133EU | sy13 3eu | sy133eu | Wrexham | Wrecsam | Fenns Bank STW | 1571 | 708 | 700to900 | 1.42 | 1.04 | 0.76 | 13.18 | 7.03 | 7.77 | 350557 | 340429 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EW | SY133EW | sy13 3ew | sy133ew | Wrexham | Wrecsam | Hanmer Arrowy STW | 915 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 345572 | 339705 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EX | SY133EX | sy13 3ex | sy133ex | Wrexham | Wrecsam | Bronington STW | 1491 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 350062 | 340234 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EY | SY133EY | sy13 3ey | sy133ey | Wrexham | Wrecsam | Fenns Bank STW | 1390 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 350067 | 339771 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3EZ | SY133EZ | sy13 3ez | sy133ez | Wrexham | Wrecsam | Fenns Bank STW | 1363 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 349894 | 338743 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3GZ | SY133GZ | sy13 3gz | sy133gz | Wrexham | Wrecsam | Bronington STW | 1241 | 718 | 700to900 | 1.44 | 1.05 | 0.77 | 13.37 | 7.13 | 7.88 | 348565 | 339472 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3HA | SY133HA | sy13 3ha | sy133ha | Wrexham | Wrecsam | Fenns Bank STW | 1791 | 718 | 700to900 | 1.44 | 1.05 | 0.77 | 13.37 | 7.13 | 7.88 | 349440 | 338999 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3HD | SY133HD | sy13 3hd | sy133hd | Wrexham | Wrecsam | Bronington STW | 1513 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 349713 | 339634 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3HE | SY133HE | sy13 3he | sy133he | Wrexham | Wrecsam | Bronington STW | 1108 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 348918 | 339635 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3HF | SY133HF | sy13 3hf | sy133hf | Wrexham | Wrecsam | Bronington STW | 756 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 348971 | 340026 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3HG | SY133HG | sy13 3hg | sy133hg | Wrexham | Wrecsam | Bronington STW | 430 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 348949 | 340401 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3HH | SY133HH | sy13 3hh | sy133hh | Wrexham | Wrecsam | Bronington STW | 1356 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 347465 | 340051 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3HJ | SY133HJ | sy13 3hj | sy133hj | Wrexham | Wrecsam | Bronington STW | 1004 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 348363 | 339748 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3HL | SY133HL | sy13 3hl | sy133hl | Wrexham | Wrecsam | Bronington STW | 1578 | 720 | 700to900 | 1.44 | 1.05 | 0.77 | 13.41 | 7.15 | 7.91 | 348261 | 339181 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3HN | SY133HN | sy13 3hn | sy133hn | Wrexham | Wrecsam | Bronington STW | 1294 | 718 | 700to900 | 1.44 | 1.05 | 0.77 | 13.37 | 7.13 | 7.88 | 348624 | 339417 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3HQ | SY133HQ | sy13 3hq | sy133hq | Wrexham | Wrecsam | Bronington STW | 646 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 348024 | 340553 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3HU | SY133HU | sy13 3hu | sy133hu | Wrexham | Wrecsam | Hanmer Arrowy STW | 1256 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 347381 | 338878 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3HY | SY133HY | sy13 3hy | sy133hy | Wrexham | Wrecsam | Hanmer Arrowy STW | 1279 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 346877 | 337942 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3JB | SY133JB | sy13 3jb | sy133jb | Wrexham | Wrecsam | Bronington STW | 1168 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 348369 | 339577 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3NZ | SY133NZ | sy13 3nz | sy133nz | Wrexham | Wrecsam | Fenns Bank STW | 304 | 713 | 700to900 | 1.43 | 1.04 | 0.76 | 13.28 | 7.08 | 7.83 | 350926 | 339010 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3PA | SY133PA | sy13 3pa | sy133pa | Wrexham | Wrecsam | Fenns Bank STW | 592 | 713 | 700to900 | 1.43 | 1.04 | 0.76 | 13.28 | 7.08 | 7.83 | 350669 | 338822 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3PB | SY133PB | sy13 3pb | sy133pb | Wrexham | Wrecsam | Fenns Bank STW | 259 | 713 | 700to900 | 1.43 | 1.04 | 0.76 | 13.28 | 7.08 | 7.83 | 350999 | 338892 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 3PE | SY133PE | sy13 3pe | sy133pe | Wrexham | Wrecsam | Fenns Bank STW | 881 | 708 | 700to900 | 1.42 | 1.04 | 0.76 | 13.18 | 7.03 | 7.77 | 350567 | 339589 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY13 4RE | SY134RE | sy13 4re | sy134re | Wrexham | Wrecsam | Bronington STW | 3443 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 350990 | 343234 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7AN | SY147AN | sy14 7an | sy147an | Wrexham | Wrecsam | Worthenbury STW | 1537 | 676 | 600to700 | 1.35 | 0.99 | 0.72 | 12.57 | 6.7 | 7.41 | 343602 | 346225 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7AZ | SY147AZ | sy14 7az | sy147az | Wrexham | Wrecsam | Worthenbury STW | 1266 | 671 | 600to700 | 1.34 | 0.98 | 0.72 | 12.47 | 6.65 | 7.35 | 343171 | 346574 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7HY | SY147HY | sy14 7hy | sy147hy | Wrexham | Wrecsam | Worthenbury STW | 3362 | 683 | 600to700 | 1.36 | 1 | 0.73 | 12.7 | 6.77 | 7.49 | 344853 | 343973 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7JH | SY147JH | sy14 7jh | sy147jh | Wrexham | Wrecsam | Worthenbury STW | 3146 | 683 | 600to700 | 1.36 | 1 | 0.73 | 12.7 | 6.77 | 7.49 | 344714 | 344151 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7JT | SY147JT | sy14 7jt | sy147jt | Wrexham | Wrecsam | Bronington STW | 2866 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 349533 | 343435 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7JU | SY147JU | sy14 7ju | sy147ju | Wrexham | Wrecsam | Bronington STW | 2908 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 348558 | 343615 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7JZ | SY147JZ | sy14 7jz | sy147jz | Wrexham | Wrecsam | Bronington STW | 3358 | 696 | 600to700 | 1.39 | 1.02 | 0.75 | 12.95 | 6.91 | 7.64 | 348213 | 344038 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LA | SY147LA | sy14 7la | sy147la | Wrexham | Wrecsam | Bronington STW | 3092 | 696 | 600to700 | 1.39 | 1.02 | 0.75 | 12.95 | 6.91 | 7.64 | 347765 | 343671 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LB | SY147LB | sy14 7lb | sy147lb | Wrexham | Wrecsam | Bronington STW | 2966 | 696 | 600to700 | 1.39 | 1.02 | 0.75 | 12.95 | 6.91 | 7.64 | 347675 | 343510 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LD | SY147LD | sy14 7ld | sy147ld | Wrexham | Wrecsam | Bronington STW | 3217 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 346462 | 343067 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LE | SY147LE | sy14 7le | sy147le | Wrexham | Wrecsam | Bronington STW | 3849 | 689 | 600to700 | 1.38 | 1.01 | 0.74 | 12.82 | 6.84 | 7.56 | 346322 | 343773 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LF | SY147LF | sy14 7lf | sy147lf | Wrexham | Wrecsam | Bronington STW | 3900 | 689 | 600to700 | 1.38 | 1.01 | 0.74 | 12.82 | 6.84 | 7.56 | 345978 | 343549 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LG | SY147LG | sy14 7lg | sy147lg | Wrexham | Wrecsam | Worthenbury STW | 3651 | 683 | 600to700 | 1.36 | 1 | 0.73 | 12.7 | 6.77 | 7.49 | 345130 | 343866 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LH | SY147LH | sy14 7lh | sy147lh | Wrexham | Wrecsam | Worthenbury STW | 3254 | 683 | 600to700 | 1.36 | 1 | 0.73 | 12.7 | 6.77 | 7.49 | 344793 | 344076 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LJ | SY147LJ | sy14 7lj | sy147lj | Wrexham | Wrecsam | Worthenbury STW | 3025 | 683 | 600to700 | 1.36 | 1 | 0.73 | 12.7 | 6.77 | 7.49 | 344612 | 344217 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LL | SY147LL | sy14 7ll | sy147ll | Wrexham | Wrecsam | Worthenbury STW | 2735 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 344399 | 344420 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LN | SY147LN | sy14 7ln | sy147ln | Wrexham | Wrecsam | Worthenbury STW | 2302 | 676 | 600to700 | 1.35 | 0.99 | 0.72 | 12.57 | 6.7 | 7.41 | 344027 | 344642 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LP | SY147LP | sy14 7lp | sy147lp | Wrexham | Wrecsam | Worthenbury STW | 1683 | 670 | 600to700 | 1.34 | 0.98 | 0.72 | 12.45 | 6.64 | 7.34 | 343053 | 344514 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LR | SY147LR | sy14 7lr | sy147lr | Wrexham | Wrecsam | Worthenbury STW | 3254 | 683 | 600to700 | 1.36 | 1 | 0.73 | 12.7 | 6.77 | 7.49 | 344239 | 343449 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LS | SY147LS | sy14 7ls | sy147ls | Wrexham | Wrecsam | Worthenbury STW | 3101 | 683 | 600to700 | 1.36 | 1 | 0.73 | 12.7 | 6.77 | 7.49 | 343899 | 343376 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LT | SY147LT | sy14 7lt | sy147lt | Wrexham | Wrecsam | Worthenbury STW | 3150 | 683 | 600to700 | 1.36 | 1 | 0.73 | 12.7 | 6.77 | 7.49 | 343689 | 343182 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LU | SY147LU | sy14 7lu | sy147lu | Wrexham | Wrecsam | Penley STW | 2928 | 684 | 600to700 | 1.37 | 1 | 0.73 | 12.72 | 6.79 | 7.5 | 343636 | 342440 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LW | SY147LW | sy14 7lw | sy147lw | Wrexham | Wrecsam | Worthenbury STW | 2304 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 343646 | 344193 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LX | SY147LX | sy14 7lx | sy147lx | Wrexham | Wrecsam | Penley STW | 2836 | 684 | 600to700 | 1.37 | 1 | 0.73 | 12.72 | 6.79 | 7.5 | 343605 | 342337 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LY | SY147LY | sy14 7ly | sy147ly | Wrexham | Wrecsam | Hanmer Arrowy STW | 3199 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 345347 | 342080 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7LZ | SY147LZ | sy14 7lz | sy147lz | Wrexham | Wrecsam | Hanmer Arrowy STW | 3340 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 345304 | 342215 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7NA | SY147NA | sy14 7na | sy147na | Wrexham | Wrecsam | Hanmer Arrowy STW | 4074 | 689 | 600to700 | 1.38 | 1.01 | 0.74 | 12.82 | 6.84 | 7.56 | 345057 | 342909 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7NB | SY147NB | sy14 7nb | sy147nb | Wrexham | Wrecsam | Worthenbury STW | 3569 | 683 | 600to700 | 1.36 | 1 | 0.73 | 12.7 | 6.77 | 7.49 | 344885 | 343670 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
SY14 7ND | SY147ND | sy14 7nd | sy147nd | Wrexham | Wrecsam | Worthenbury STW | 4160 | 689 | 600to700 | 1.38 | 1.01 | 0.74 | 12.82 | 6.84 | 7.56 | 345684 | 343791 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LD3 0EP | LD30EP | ld3 0ep | ld30ep | Powys | Powys | Talgarth STW | 5831 | 1117 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.82 | 11.1 | 12.27 | 317443 | 229480 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0ER | LD30ER | ld3 0er | ld30er | Powys | Powys | Cwmdu STW | 5050 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 318196 | 228337 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0ES | LD30ES | ld3 0es | ld30es | Powys | Powys | Cwmdu STW | 4533 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 318985 | 227687 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0ET | LD30ET | ld3 0et | ld30et | Powys | Powys | Talgarth STW | 6009 | 1125 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.97 | 11.18 | 12.36 | 318695 | 230014 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0EU | LD30EU | ld3 0eu | ld30eu | Powys | Powys | Cwmdu STW | 5728 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 318241 | 229013 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0TP | LD30TP | ld3 0tp | ld30tp | Powys | Powys | Llanddew STW | 2394 | 1115 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.78 | 11.08 | 12.25 | 307416 | 230120 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 0TR | LD30TR | ld3 0tr | ld30tr | Powys | Powys | Llanddew STW | 1890 | 1115 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.78 | 11.08 | 12.25 | 306917 | 230217 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0TS | LD30TS | ld3 0ts | ld30ts | Powys | Powys | Llanddew STW | 2966 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 308084 | 231085 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 0TW | LD30TW | ld3 0tw | ld30tw | Powys | Powys | Groesffordd STW | 2441 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 308315 | 229830 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 3DE | LD33DE | ld3 3de | ld33de | Powys | Powys | Llanspyddid STW | 2003 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303055 | 227907 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 3DG | LD33DG | ld3 3dg | ld33dg | Powys | Powys | Llanspyddid STW | 2003 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303055 | 227907 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 3DP | LD33DP | ld3 3dp | ld33dp | Powys | Powys | Llanspyddid STW | 2003 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303055 | 227907 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 3DQ | LD33DQ | ld3 3dq | ld33dq | Powys | Powys | Llanspyddid STW | 2003 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303055 | 227907 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 3DR | LD33DR | ld3 3dr | ld33dr | Powys | Powys | Llanspyddid STW | 2003 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303055 | 227907 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AA | LD37AA | ld3 7aa | ld37aa | Powys | Powys | Brecon STW | 1743 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304448 | 228525 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AD | LD37AD | ld3 7ad | ld37ad | Powys | Powys | Brecon STW | 1613 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304572 | 228479 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AE | LD37AE | ld3 7ae | ld37ae | Powys | Powys | Brecon STW | 1622 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304563 | 228482 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AF | LD37AF | ld3 7af | ld37af | Powys | Powys | Brecon STW | 1656 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304532 | 228495 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AG | LD37AG | ld3 7ag | ld37ag | Powys | Powys | Brecon STW | 1682 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304540 | 228555 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AH | LD37AH | ld3 7ah | ld37ah | Powys | Powys | Brecon STW | 1702 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304525 | 228568 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AJ | LD37AJ | ld3 7aj | ld37aj | Powys | Powys | Llanfyrnach STW | 436 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 307417 | 225879 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AL | LD37AL | ld3 7al | ld37al | Powys | Powys | Brecon STW | 1754 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304487 | 228604 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AN | LD37AN | ld3 7an | ld37an | Powys | Powys | Brecon STW | 1802 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304442 | 228624 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AP | LD37AP | ld3 7ap | ld37ap | Powys | Powys | Brecon STW | 1751 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304471 | 228575 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AQ | LD37AQ | ld3 7aq | ld37aq | Powys | Powys | Groesffordd STW | 695 | 1174 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.88 | 11.67 | 12.9 | 306926 | 227045 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AR | LD37AR | ld3 7ar | ld37ar | Powys | Powys | Brecon STW | 1775 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304458 | 228600 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AS | LD37AS | ld3 7as | ld37as | Powys | Powys | Brecon STW | 1715 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304499 | 228553 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AU | LD37AU | ld3 7au | ld37au | Powys | Powys | Brecon STW | 1592 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304606 | 228491 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AX | LD37AX | ld3 7ax | ld37ax | Powys | Powys | Llanfyrnach STW | 1006 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 306847 | 225760 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AY | LD37AY | ld3 7ay | ld37ay | Powys | Powys | Brecon STW | 1691 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304538 | 228567 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7AZ | LD37AZ | ld3 7az | ld37az | Powys | Powys | Llanfyrnach STW | 395 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 307464 | 225746 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BA | LD37BA | ld3 7ba | ld37ba | Powys | Powys | Brecon STW | 1672 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304586 | 228601 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BD | LD37BD | ld3 7bd | ld37bd | Powys | Powys | Llanfyrnach STW | 231 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 307644 | 225725 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BE | LD37BE | ld3 7be | ld37be | Powys | Powys | Brecon STW | 926 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305180 | 228150 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BF | LD37BF | ld3 7bf | ld37bf | Powys | Powys | Brecon STW | 511 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305573 | 227969 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BG | LD37BG | ld3 7bg | ld37bg | Powys | Powys | Brecon STW | 1446 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304724 | 228406 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BH | LD37BH | ld3 7bh | ld37bh | Powys | Powys | Brecon STW | 1668 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304557 | 228554 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BJ | LD37BJ | ld3 7bj | ld37bj | Powys | Powys | Llanfyrnach STW | 378 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 307504 | 225679 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BL | LD37BL | ld3 7bl | ld37bl | Powys | Powys | Brecon STW | 1460 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304747 | 228462 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BN | LD37BN | ld3 7bn | ld37bn | Powys | Powys | Brecon STW | 1481 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304716 | 228456 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BQ | LD37BQ | ld3 7bq | ld37bq | Powys | Powys | Llanfyrnach STW | 552 | 1248 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.26 | 12.41 | 13.71 | 307606 | 225335 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BS | LD37BS | ld3 7bs | ld37bs | Powys | Powys | Llanfyrnach STW | 455 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 307971 | 226268 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BU | LD37BU | ld3 7bu | ld37bu | Powys | Powys | Brecon STW | 1431 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304854 | 228548 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BX | LD37BX | ld3 7bx | ld37bx | Powys | Powys | Llanfyrnach STW | 313 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 307552 | 225733 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BY | LD37BY | ld3 7by | ld37by | Powys | Powys | Brecon STW | 1260 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305082 | 228535 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7BZ | LD37BZ | ld3 7bz | ld37bz | Powys | Powys | Llanfyrnach STW | 216 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 307634 | 225833 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DA | LD37DA | ld3 7da | ld37da | Powys | Powys | Brecon STW | 1024 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305230 | 228350 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DB | LD37DB | ld3 7db | ld37db | Powys | Powys | Brecon STW | 1024 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305230 | 228350 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DD | LD37DD | ld3 7dd | ld37dd | Powys | Powys | Brecon STW | 1472 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304616 | 228276 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DE | LD37DE | ld3 7de | ld37de | Powys | Powys | Brecon STW | 1491 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304550 | 228179 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DG | LD37DG | ld3 7dg | ld37dg | Powys | Powys | Brecon STW | 1780 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304422 | 228554 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DH | LD37DH | ld3 7dh | ld37dh | Powys | Powys | Brecon STW | 1744 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304459 | 228544 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DJ | LD37DJ | ld3 7dj | ld37dj | Powys | Powys | Brecon STW | 1706 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304504 | 228545 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DL | LD37DL | ld3 7dl | ld37dl | Powys | Powys | Brecon STW | 1757 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 304409 | 228488 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DQ | LD37DQ | ld3 7dq | ld37dq | Powys | Powys | Llanfyrnach STW | 1613 | 1552 | Over1500 | 3.11 | 2.27 | 1.67 | 28.93 | 15.43 | 17.05 | 307954 | 224221 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DR | LD37DR | ld3 7dr | ld37dr | Powys | Powys | Llanfyrnach STW | 987 | 1248 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.26 | 12.41 | 13.71 | 308114 | 224879 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DS | LD37DS | ld3 7ds | ld37ds | Powys | Powys | Brecon STW | 1662 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 304448 | 228364 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DT | LD37DT | ld3 7dt | ld37dt | Powys | Powys | Brecon STW | 1531 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304604 | 228374 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DU | LD37DU | ld3 7du | ld37du | Powys | Powys | Brecon STW | 1580 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304537 | 228357 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DW | LD37DW | ld3 7dw | ld37dw | Powys | Powys | Brecon STW | 1637 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304528 | 228453 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DX | LD37DX | ld3 7dx | ld37dx | Powys | Powys | Brecon STW | 1590 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 304481 | 228269 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7DY | LD37DY | ld3 7dy | ld37dy | Powys | Powys | Brecon STW | 1633 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 304474 | 228350 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EA | LD37EA | ld3 7ea | ld37ea | Powys | Powys | Brecon STW | 1099 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304994 | 228184 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EB | LD37EB | ld3 7eb | ld37eb | Powys | Powys | Brecon STW | 1137 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304981 | 228234 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7ED | LD37ED | ld3 7ed | ld37ed | Powys | Powys | Brecon STW | 1294 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304839 | 228304 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EE | LD37EE | ld3 7ee | ld37ee | Powys | Powys | Brecon STW | 1277 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304920 | 228387 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EF | LD37EF | ld3 7ef | ld37ef | Powys | Powys | Brecon STW | 1461 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304700 | 228397 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EG | LD37EG | ld3 7eg | ld37eg | Powys | Powys | Brecon STW | 1445 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304700 | 228367 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EH | LD37EH | ld3 7eh | ld37eh | Powys | Powys | Brecon STW | 1455 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304662 | 228323 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EJ | LD37EJ | ld3 7ej | ld37ej | Powys | Powys | Pennorth And Scethrog STW | 1225 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 311140 | 225972 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EL | LD37EL | ld3 7el | ld37el | Powys | Powys | Brecon STW | 1257 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304852 | 228256 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EN | LD37EN | ld3 7en | ld37en | Powys | Powys | Brecon STW | 1089 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304987 | 228154 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EP | LD37EP | ld3 7ep | ld37ep | Powys | Powys | Brecon STW | 798 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305235 | 228003 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EQ | LD37EQ | ld3 7eq | ld37eq | Powys | Powys | Pennorth And Scethrog STW | 404 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 310646 | 225254 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7ER | LD37ER | ld3 7er | ld37er | Powys | Powys | Brecon STW | 1489 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304644 | 228360 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7ES | LD37ES | ld3 7es | ld37es | Powys | Powys | Brecon STW | 1475 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304663 | 228365 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7ET | LD37ET | ld3 7et | ld37et | Powys | Powys | Brecon STW | 1270 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304874 | 228313 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EU | LD37EU | ld3 7eu | ld37eu | Powys | Powys | Brecon STW | 1364 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304743 | 228281 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EW | LD37EW | ld3 7ew | ld37ew | Powys | Powys | Brecon STW | 1389 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304661 | 228178 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EY | LD37EY | ld3 7ey | ld37ey | Powys | Powys | Brecon STW | 1368 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304706 | 228223 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7FB | LD37FB | ld3 7fb | ld37fb | Powys | Powys | Brecon STW | 1097 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305258 | 228468 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7FD | LD37FD | ld3 7fd | ld37fd | Powys | Powys | Brecon STW | 1424 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304657 | 228249 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7FE | LD37FE | ld3 7fe | ld37fe | Powys | Powys | Brecon STW | 1313 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304794 | 228267 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7FG | LD37FG | ld3 7fg | ld37fg | Powys | Powys | Brecon STW | 1330 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304742 | 228210 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7GA | LD37GA | ld3 7ga | ld37ga | Powys | Powys | Brecon STW | 1579 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304640 | 228518 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HA | LD37HA | ld3 7ha | ld37ha | Powys | Powys | Brecon STW | 1251 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304840 | 228223 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HB | LD37HB | ld3 7hb | ld37hb | Powys | Powys | Brecon STW | 1218 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304947 | 228325 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HD | LD37HD | ld3 7hd | ld37hd | Powys | Powys | Brecon STW | 1155 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304914 | 228159 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HE | LD37HE | ld3 7he | ld37he | Powys | Powys | Brecon STW | 1227 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304851 | 228194 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HF | LD37HF | ld3 7hf | ld37hf | Powys | Powys | Brecon STW | 1208 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304871 | 228191 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HG | LD37HG | ld3 7hg | ld37hg | Powys | Powys | Brecon STW | 1046 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304982 | 228056 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HH | LD37HH | ld3 7hh | ld37hh | Powys | Powys | Brecon STW | 808 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305200 | 227960 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HJ | LD37HJ | ld3 7hj | ld37hj | Powys | Powys | Bwlch (S) STW | 2275 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 314585 | 222382 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HL | LD37HL | ld3 7hl | ld37hl | Powys | Powys | Brecon STW | 1402 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304621 | 228119 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HN | LD37HN | ld3 7hn | ld37hn | Powys | Powys | Bwlch (S) STW | 2120 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 314706 | 222265 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HP | LD37HP | ld3 7hp | ld37hp | Powys | Powys | Brecon STW | 820 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305262 | 228083 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HR | LD37HR | ld3 7hr | ld37hr | Powys | Powys | Brecon STW | 1073 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305092 | 228276 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HT | LD37HT | ld3 7ht | ld37ht | Powys | Powys | Llanfyrnach STW | 505 | 1248 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.26 | 12.41 | 13.71 | 307526 | 225443 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HU | LD37HU | ld3 7hu | ld37hu | Powys | Powys | Brecon STW | 1194 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304850 | 228123 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HW | LD37HW | ld3 7hw | ld37hw | Powys | Powys | Brecon STW | 1491 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304550 | 228179 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HX | LD37HX | ld3 7hx | ld37hx | Powys | Powys | Bwlch (S) STW | 1950 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 314755 | 222101 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HY | LD37HY | ld3 7hy | ld37hy | Powys | Powys | Brecon STW | 1753 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304505 | 228627 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HZ | LD37HZ | ld3 7hz | ld37hz | Powys | Powys | Bwlch (S) STW | 1923 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 315148 | 222190 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JA | LD37JA | ld3 7ja | ld37ja | Powys | Powys | Talybont STW | 765 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 311448 | 222609 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JB | LD37JB | ld3 7jb | ld37jb | Powys | Powys | Talybont STW | 801 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 311417 | 222591 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JD | LD37JD | ld3 7jd | ld37jd | Powys | Powys | Talybont STW | 772 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 311497 | 222538 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JE | LD37JE | ld3 7je | ld37je | Powys | Powys | Talybont STW | 351 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 311799 | 222832 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JF | LD37JF | ld3 7jf | ld37jf | Powys | Powys | Talybont STW | 473 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 311769 | 222691 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JG | LD37JG | ld3 7jg | ld37jg | Powys | Powys | Talybont STW | 390 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 311795 | 222779 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JH | LD37JH | ld3 7jh | ld37jh | Powys | Powys | Talybont STW | 609 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 311653 | 222612 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JJ | LD37JJ | ld3 7jj | ld37jj | Powys | Powys | Talybont STW | 1865 | 1248 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.26 | 12.41 | 13.71 | 313319 | 221672 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JL | LD37JL | ld3 7jl | ld37jl | Powys | Powys | Talybont STW | 2191 | 1154 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.51 | 11.47 | 12.68 | 314148 | 222366 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JP | LD37JP | ld3 7jp | ld37jp | Powys | Powys | Brecon STW | 1723 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304544 | 228630 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JQ | LD37JQ | ld3 7jq | ld37jq | Powys | Powys | Talybont STW | 1091 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 313116 | 222752 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JU | LD37JU | ld3 7ju | ld37ju | Powys | Powys | Brecon STW | 609 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305478 | 228013 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JW | LD37JW | ld3 7jw | ld37jw | Powys | Powys | Llanddew STW | 1834 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304633 | 229065 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LA | LD37LA | ld3 7la | ld37la | Powys | Powys | Brecon STW | 1809 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304470 | 228674 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LB | LD37LB | ld3 7lb | ld37lb | Powys | Powys | Brecon STW | 1609 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304592 | 228501 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LD | LD37LD | ld3 7ld | ld37ld | Powys | Powys | Brecon STW | 1828 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304489 | 228730 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LE | LD37LE | ld3 7le | ld37le | Powys | Powys | Brecon STW | 1841 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304445 | 228694 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LF | LD37LF | ld3 7lf | ld37lf | Powys | Powys | Brecon STW | 1832 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304445 | 228680 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LH | LD37LH | ld3 7lh | ld37lh | Powys | Powys | Brecon STW | 1829 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304469 | 228706 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LJ | LD37LJ | ld3 7lj | ld37lj | Powys | Powys | Llanfyrnach STW | 857 | 1121 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.89 | 11.14 | 12.32 | 308692 | 225986 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LL | LD37LL | ld3 7ll | ld37ll | Powys | Powys | Brecon STW | 1880 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304500 | 228825 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LN | LD37LN | ld3 7ln | ld37ln | Powys | Powys | Llanddew STW | 1851 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304646 | 229044 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LP | LD37LP | ld3 7lp | ld37lp | Powys | Powys | Llanddew STW | 1934 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304563 | 228982 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LQ | LD37LQ | ld3 7lq | ld37lq | Powys | Powys | Llanfyrnach STW | 1178 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 307023 | 224991 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LS | LD37LS | ld3 7ls | ld37ls | Powys | Powys | Brecon STW | 1905 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304482 | 228842 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LT | LD37LT | ld3 7lt | ld37lt | Powys | Powys | Brecon STW | 1856 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304459 | 228737 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LU | LD37LU | ld3 7lu | ld37lu | Powys | Powys | Brecon STW | 1795 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304549 | 228752 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LW | LD37LW | ld3 7lw | ld37lw | Powys | Powys | Brecon STW | 1920 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304551 | 228939 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LX | LD37LX | ld3 7lx | ld37lx | Powys | Powys | Pencelli STW | 536 | 1126 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.99 | 11.19 | 12.37 | 309284 | 224805 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LY | LD37LY | ld3 7ly | ld37ly | Powys | Powys | Brecon STW | 1757 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304600 | 228752 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7LZ | LD37LZ | ld3 7lz | ld37lz | Powys | Powys | STP @ Cross Oak | 578 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 310134 | 224143 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NA | LD37NA | ld3 7na | ld37na | Powys | Powys | Brecon STW | 1789 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304625 | 228827 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NB | LD37NB | ld3 7nb | ld37nb | Powys | Powys | Brecon STW | 1888 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304533 | 228874 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7ND | LD37ND | ld3 7nd | ld37nd | Powys | Powys | Brecon STW | 1863 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304578 | 228886 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NE | LD37NE | ld3 7ne | ld37ne | Powys | Powys | Brecon STW | 1726 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304673 | 228786 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NF | LD37NF | ld3 7nf | ld37nf | Powys | Powys | Brecon STW | 1717 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304754 | 228854 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NG | LD37NG | ld3 7ng | ld37ng | Powys | Powys | Brecon STW | 1760 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304680 | 228842 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NH | LD37NH | ld3 7nh | ld37nh | Powys | Powys | Brecon STW | 1722 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304730 | 228838 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NJ | LD37NJ | ld3 7nj | ld37nj | Powys | Powys | Bwlch (S) STW | 1474 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 315022 | 221694 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NL | LD37NL | ld3 7nl | ld37nl | Powys | Powys | Llanddew STW | 1854 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304730 | 229020 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NN | LD37NN | ld3 7nn | ld37nn | Powys | Powys | Brecon STW | 1814 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304811 | 229029 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NP | LD37NP | ld3 7np | ld37np | Powys | Powys | Brecon STW | 1633 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304920 | 228884 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NQ | LD37NQ | ld3 7nq | ld37nq | Powys | Powys | Bwlch (S) STW | 1653 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 314964 | 221863 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NR | LD37NR | ld3 7nr | ld37nr | Powys | Powys | Brecon STW | 1561 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304845 | 228725 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NS | LD37NS | ld3 7ns | ld37ns | Powys | Powys | Brecon STW | 1530 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304921 | 228753 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NT | LD37NT | ld3 7nt | ld37nt | Powys | Powys | Brecon STW | 1497 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304835 | 228624 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NU | LD37NU | ld3 7nu | ld37nu | Powys | Powys | Pencelli STW | 307 | 1126 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.99 | 11.19 | 12.37 | 309444 | 225059 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NW | LD37NW | ld3 7nw | ld37nw | Powys | Powys | Brecon STW | 1716 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304826 | 228915 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NX | LD37NX | ld3 7nx | ld37nx | Powys | Powys | Bwlch (S) STW | 1053 | 1222 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.78 | 12.15 | 13.43 | 314981 | 221216 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NY | LD37NY | ld3 7ny | ld37ny | Powys | Powys | Brecon STW | 1611 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304768 | 228719 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7NZ | LD37NZ | ld3 7nz | ld37nz | Powys | Powys | Bwlch (S) STW | 1056 | 1281 | 1200to1500 | 2.56 | 1.88 | 1.38 | 23.88 | 12.73 | 14.07 | 314444 | 220299 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PA | LD37PA | ld3 7pa | ld37pa | Powys | Powys | Brecon STW | 1650 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304794 | 228799 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PB | LD37PB | ld3 7pb | ld37pb | Powys | Powys | Brecon STW | 1543 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304765 | 228616 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PD | LD37PD | ld3 7pd | ld37pd | Powys | Powys | Brecon STW | 1638 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304704 | 228690 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PE | LD37PE | ld3 7pe | ld37pe | Powys | Powys | Brecon STW | 1887 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304419 | 228737 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PF | LD37PF | ld3 7pf | ld37pf | Powys | Powys | Brecon STW | 881 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305137 | 227997 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PG | LD37PG | ld3 7pg | ld37pg | Powys | Powys | Brecon STW | 1601 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304881 | 228811 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PL | LD37PL | ld3 7pl | ld37pl | Powys | Powys | Brecon STW | 500 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305536 | 227914 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PN | LD37PN | ld3 7pn | ld37pn | Powys | Powys | Brecon STW | 451 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305949 | 228045 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PP | LD37PP | ld3 7pp | ld37pp | Powys | Powys | Brecon STW | 513 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305885 | 228107 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PR | LD37PR | ld3 7pr | ld37pr | Powys | Powys | Brecon STW | 694 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 306171 | 228242 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PS | LD37PS | ld3 7ps | ld37ps | Powys | Powys | Brecon STW | 732 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 306253 | 228247 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PT | LD37PT | ld3 7pt | ld37pt | Powys | Powys | Brecon STW | 783 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 306262 | 228300 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PW | LD37PW | ld3 7pw | ld37pw | Powys | Powys | Brecon STW | 506 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305946 | 228100 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7QA | LD37QA | ld3 7qa | ld37qa | Powys | Powys | Brecon STW | 1843 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304481 | 228744 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RA | LD37RA | ld3 7ra | ld37ra | Powys | Powys | Brecon STW | 501 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 306264 | 227960 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RB | LD37RB | ld3 7rb | ld37rb | Powys | Powys | Brecon STW | 501 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 306264 | 227960 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RD | LD37RD | ld3 7rd | ld37rd | Powys | Powys | Brecon STW | 664 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 306127 | 228226 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RE | LD37RE | ld3 7re | ld37re | Powys | Powys | Brecon STW | 434 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 306135 | 227973 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RH | LD37RH | ld3 7rh | ld37rh | Powys | Powys | Brecon STW | 283 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305924 | 227878 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RJ | LD37RJ | ld3 7rj | ld37rj | Powys | Powys | Bwlch (S) STW | 1635 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 314887 | 221815 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RL | LD37RL | ld3 7rl | ld37rl | Powys | Powys | Brecon STW | 382 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305904 | 227977 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RN | LD37RN | ld3 7rn | ld37rn | Powys | Powys | Brecon STW | 458 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305780 | 228031 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RP | LD37RP | ld3 7rp | ld37rp | Powys | Powys | Brecon STW | 631 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305511 | 228075 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RQ | LD37RQ | ld3 7rq | ld37rq | Powys | Powys | Bwlch (S) STW | 1810 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 314983 | 222034 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RR | LD37RR | ld3 7rr | ld37rr | Powys | Powys | Brecon STW | 689 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305489 | 228131 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RS | LD37RS | ld3 7rs | ld37rs | Powys | Powys | Brecon STW | 1277 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304997 | 228476 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RT | LD37RT | ld3 7rt | ld37rt | Powys | Powys | Brecon STW | 954 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305232 | 228254 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RU | LD37RU | ld3 7ru | ld37ru | Powys | Powys | Brecon STW | 367 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305972 | 227958 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RW | LD37RW | ld3 7rw | ld37rw | Powys | Powys | Brecon STW | 532 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305639 | 228046 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RX | LD37RX | ld3 7rx | ld37rx | Powys | Powys | Bwlch (S) STW | 1382 | 1222 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.78 | 12.15 | 13.43 | 314757 | 221465 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7RZ | LD37RZ | ld3 7rz | ld37rz | Powys | Powys | Bwlch (S) STW | 1714 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 314954 | 221924 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SA | LD37SA | ld3 7sa | ld37sa | Powys | Powys | Brecon STW | 864 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 305334 | 228228 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SB | LD37SB | ld3 7sb | ld37sb | Powys | Powys | Bwlch (S) STW | 1771 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 315375 | 222066 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SD | LD37SD | ld3 7sd | ld37sd | Powys | Powys | Llanfyrnach STW | 337 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 307541 | 225695 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SE | LD37SE | ld3 7se | ld37se | Powys | Powys | Brecon STW | 1559 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304696 | 228559 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SF | LD37SF | ld3 7sf | ld37sf | Powys | Powys | Groesffordd STW | 642 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 307503 | 228208 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 7SG | LD37SG | ld3 7sg | ld37sg | Powys | Powys | Brecon STW | 365 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 306082 | 227922 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SH | LD37SH | ld3 7sh | ld37sh | Powys | Powys | Groesffordd STW | 487 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 306997 | 227893 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SJ | LD37SJ | ld3 7sj | ld37sj | Powys | Powys | Bwlch (S) STW | 1851 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 315373 | 222146 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SL | LD37SL | ld3 7sl | ld37sl | Powys | Powys | Groesffordd STW | 293 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 307648 | 227489 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SN | LD37SN | ld3 7sn | ld37sn | Powys | Powys | Groesffordd STW | 439 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 307556 | 227978 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 7SP | LD37SP | ld3 7sp | ld37sp | Powys | Powys | Groesffordd STW | 1151 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 308004 | 228540 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 7SQ | LD37SQ | ld3 7sq | ld37sq | Powys | Powys | Bwlch (S) STW | 1643 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 315598 | 221940 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SR | LD37SR | ld3 7sr | ld37sr | Powys | Powys | Llanddew STW | 1376 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305002 | 229460 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SS | LD37SS | ld3 7ss | ld37ss | Powys | Powys | Llanddew STW | 1037 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 305063 | 229795 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7ST | LD37ST | ld3 7st | ld37st | Powys | Powys | Brecon STW | 434 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 306192 | 227934 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SU | LD37SU | ld3 7su | ld37su | Powys | Powys | Groesffordd STW | 1435 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 308765 | 227914 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 7SW | LD37SW | ld3 7sw | ld37sw | Powys | Powys | Groesffordd STW | 1081 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 307374 | 228661 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 7UQ | LD37UQ | ld3 7uq | ld37uq | Powys | Powys | STP @ Cross Oak | 309 | 1152 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.47 | 11.45 | 12.66 | 310795 | 223632 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UX | LD37UX | ld3 7ux | ld37ux | Powys | Powys | Talybont STW | 910 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 311159 | 223056 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UY | LD37UY | ld3 7uy | ld37uy | Powys | Powys | Groesffordd STW | 466 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 307656 | 227212 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UZ | LD37UZ | ld3 7uz | ld37uz | Powys | Powys | Talybont STW | 870 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 311227 | 222838 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7WD | LD37WD | ld3 7wd | ld37wd | Powys | Powys | Llanspyddid STW | 2003 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303055 | 227907 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YA | LD37YA | ld3 7ya | ld37ya | Powys | Powys | Llanfyrnach STW | 1524 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 308922 | 226913 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YB | LD37YB | ld3 7yb | ld37yb | Powys | Powys | Pencelli STW | 1138 | 1121 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.89 | 11.14 | 12.32 | 309124 | 226461 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YD | LD37YD | ld3 7yd | ld37yd | Powys | Powys | Pencelli STW | 768 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 309528 | 226079 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YE | LD37YE | ld3 7ye | ld37ye | Powys | Powys | Pennorth And Scethrog STW | 208 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 310463 | 224942 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YF | LD37YF | ld3 7yf | ld37yf | Powys | Powys | Talybont STW | 552 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 312216 | 223588 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YG | LD37YG | ld3 7yg | ld37yg | Powys | Powys | Pennorth And Scethrog STW | 972 | 1121 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.89 | 11.14 | 12.32 | 311581 | 224571 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YJ | LD37YJ | ld3 7yj | ld37yj | Powys | Powys | Talybont STW | 819 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 311313 | 222741 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YL | LD37YL | ld3 7yl | ld37yl | Powys | Powys | Talybont STW | 810 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 311345 | 222694 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YN | LD37YN | ld3 7yn | ld37yn | Powys | Powys | STP @ Cross Oak | 822 | 1398 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.06 | 13.9 | 15.36 | 310366 | 223145 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YP | LD37YP | ld3 7yp | ld37yp | Powys | Powys | Talybont STW | 705 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 311756 | 222425 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YQ | LD37YQ | ld3 7yq | ld37yq | Powys | Powys | Talybont STW | 807 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 311311 | 222780 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YR | LD37YR | ld3 7yr | ld37yr | Powys | Powys | Aber STW | 2079 | 1429 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.63 | 14.2 | 15.7 | 312456 | 220585 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YS | LD37YS | ld3 7ys | ld37ys | Powys | Powys | Aber STW | 325 | 1576 | Over1500 | 3.15 | 2.31 | 1.69 | 29.37 | 15.67 | 17.32 | 310280 | 221356 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YT | LD37YT | ld3 7yt | ld37yt | Powys | Powys | Aber STW | 2950 | 1637 | Over1500 | 3.28 | 2.4 | 1.76 | 30.51 | 16.27 | 17.99 | 310304 | 218544 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YU | LD37YU | ld3 7yu | ld37yu | Powys | Powys | Aber STW | 1223 | 1429 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.63 | 14.2 | 15.7 | 311743 | 221103 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YW | LD37YW | ld3 7yw | ld37yw | Powys | Powys | Aber STW | 1161 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 310757 | 222627 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YX | LD37YX | ld3 7yx | ld37yx | Powys | Powys | Talybont STW | 785 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 311402 | 222643 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7YZ | LD37YZ | ld3 7yz | ld37yz | Powys | Powys | Talybont STW | 785 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 311420 | 222614 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7ZZ | LD37ZZ | ld3 7zz | ld37zz | Powys | Powys | Llanspyddid STW | 2006 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303059 | 227907 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AD | LD38AD | ld3 8ad | ld38ad | Powys | Powys | Brecon STW | 1843 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 304286 | 228445 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AF | LD38AF | ld3 8af | ld38af | Powys | Powys | Brecon STW | 1919 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 304195 | 228432 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AH | LD38AH | ld3 8ah | ld38ah | Powys | Powys | Brecon STW | 1993 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304177 | 228559 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AJ | LD38AJ | ld3 8aj | ld38aj | Powys | Powys | Cray STW | 2140 | 1796 | Over1500 | 3.59 | 2.63 | 1.93 | 33.47 | 17.85 | 19.73 | 288902 | 226334 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AL | LD38AL | ld3 8al | ld38al | Powys | Powys | Brecon STW | 2110 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303982 | 228425 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AN | LD38AN | ld3 8an | ld38an | Powys | Powys | Brecon STW | 2075 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 304052 | 228495 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AP | LD38AP | ld3 8ap | ld38ap | Powys | Powys | Brecon STW | 2081 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303979 | 228341 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AQ | LD38AQ | ld3 8aq | ld38aq | Powys | Powys | Brecon STW | 1646 | 1273 | 1200to1500 | 2.55 | 1.86 | 1.37 | 23.73 | 12.65 | 13.99 | 304288 | 227392 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AR | LD38AR | ld3 8ar | ld38ar | Powys | Powys | Brecon STW | 2194 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303881 | 228401 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AS | LD38AS | ld3 8as | ld38as | Powys | Powys | Brecon STW | 2194 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303888 | 228419 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AT | LD38AT | ld3 8at | ld38at | Powys | Powys | Brecon STW | 2202 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303889 | 228442 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AU | LD38AU | ld3 8au | ld38au | Powys | Powys | Brecon STW | 2204 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303938 | 228555 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AW | LD38AW | ld3 8aw | ld38aw | Powys | Powys | Brecon STW | 2137 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303954 | 228428 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8AY | LD38AY | ld3 8ay | ld38ay | Powys | Powys | Brecon STW | 2189 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303916 | 228473 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8BA | LD38BA | ld3 8ba | ld38ba | Powys | Powys | Brecon STW | 2213 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303951 | 228602 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8BB | LD38BB | ld3 8bb | ld38bb | Powys | Powys | Brecon STW | 2165 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303953 | 228495 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8BD | LD38BD | ld3 8bd | ld38bd | Powys | Powys | Brecon STW | 2187 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304010 | 228657 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8BE | LD38BE | ld3 8be | ld38be | Powys | Powys | Brecon STW | 2251 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303951 | 228683 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8BG | LD38BG | ld3 8bg | ld38bg | Powys | Powys | Brecon STW | 2340 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303830 | 228644 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8BH | LD38BH | ld3 8bh | ld38bh | Powys | Powys | Sennybridge Army Camp STW | 387 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 292150 | 229375 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8BL | LD38BL | ld3 8bl | ld38bl | Powys | Powys | Brecon STW | 2065 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304102 | 228571 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8BN | LD38BN | ld3 8bn | ld38bn | Powys | Powys | Brecon STW | 1808 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 304313 | 228421 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8BT | LD38BT | ld3 8bt | ld38bt | Powys | Powys | Llanspyddid STW | 1803 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 302886 | 228136 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8BU | LD38BU | ld3 8bu | ld38bu | Powys | Powys | Brecon STW | 2176 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303902 | 228405 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8BY | LD38BY | ld3 8by | ld38by | Powys | Powys | Brecon STW | 2195 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303867 | 228368 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DA | LD38DA | ld3 8da | ld38da | Powys | Powys | Brecon STW | 2317 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303746 | 228391 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DB | LD38DB | ld3 8db | ld38db | Powys | Powys | Brecon STW | 2279 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303819 | 228474 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DD | LD38DD | ld3 8dd | ld38dd | Powys | Powys | Brecon STW | 2414 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303650 | 228411 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DE | LD38DE | ld3 8de | ld38de | Powys | Powys | Llanspyddid STW | 2464 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303551 | 228386 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DF | LD38DF | ld3 8df | ld38df | Powys | Powys | Brecon STW | 2361 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303762 | 228548 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DG | LD38DG | ld3 8dg | ld38dg | Powys | Powys | Brecon STW | 2408 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303631 | 228338 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DH | LD38DH | ld3 8dh | ld38dh | Powys | Powys | Brecon STW | 2358 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303687 | 228348 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DJ | LD38DJ | ld3 8dj | ld38dj | Powys | Powys | Llanspyddid STW | 2415 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303504 | 228264 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DL | LD38DL | ld3 8dl | ld38dl | Powys | Powys | Brecon STW | 2397 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303633 | 228306 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DN | LD38DN | ld3 8dn | ld38dn | Powys | Powys | Llanspyddid STW | 2398 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303487 | 228326 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DP | LD38DP | ld3 8dp | ld38dp | Powys | Powys | Llanspyddid STW | 2450 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303538 | 228211 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DQ | LD38DQ | ld3 8dq | ld38dq | Powys | Powys | Llanspyddid STW | 2425 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303513 | 228379 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DR | LD38DR | ld3 8dr | ld38dr | Powys | Powys | Llanspyddid STW | 2420 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303508 | 228216 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DS | LD38DS | ld3 8ds | ld38ds | Powys | Powys | Brecon STW | 2239 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303773 | 228223 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DT | LD38DT | ld3 8dt | ld38dt | Powys | Powys | Brecon STW | 2315 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303677 | 228162 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DU | LD38DU | ld3 8du | ld38du | Powys | Powys | Brecon STW | 2352 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303658 | 228234 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DW | LD38DW | ld3 8dw | ld38dw | Powys | Powys | Llanspyddid STW | 2362 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303451 | 228295 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DX | LD38DX | ld3 8dx | ld38dx | Powys | Powys | Llanspyddid STW | 2438 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303521 | 228459 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8DY | LD38DY | ld3 8dy | ld38dy | Powys | Powys | Brecon STW | 2410 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303568 | 228114 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EA | LD38EA | ld3 8ea | ld38ea | Powys | Powys | Brecon STW | 2238 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303737 | 228080 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EB | LD38EB | ld3 8eb | ld38eb | Powys | Powys | Brecon STW | 2207 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303832 | 228304 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8ED | LD38ED | ld3 8ed | ld38ed | Powys | Powys | Llanspyddid STW | 2268 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303357 | 228313 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EE | LD38EE | ld3 8ee | ld38ee | Powys | Powys | Brecon STW | 2235 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303758 | 228155 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EF | LD38EF | ld3 8ef | ld38ef | Powys | Powys | Llanspyddid STW | 1625 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 302711 | 228401 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EG | LD38EG | ld3 8eg | ld38eg | Powys | Powys | Llanspyddid STW | 2202 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303290 | 228367 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EH | LD38EH | ld3 8eh | ld38eh | Powys | Powys | Llanspyddid STW | 1319 | 1266 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.6 | 12.58 | 13.91 | 301697 | 227119 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EJ | LD38EJ | ld3 8ej | ld38ej | Powys | Powys | Libanus WwTW | 341 | 1406 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.21 | 13.98 | 15.45 | 299442 | 226077 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EL | LD38EL | ld3 8el | ld38el | Powys | Powys | Libanus WwTW | 317 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 299882 | 226336 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EN | LD38EN | ld3 8en | ld38en | Powys | Powys | Libanus WwTW | 446 | 1406 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.21 | 13.98 | 15.45 | 299340 | 225965 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EP | LD38EP | ld3 8ep | ld38ep | Powys | Powys | Libanus WwTW | 1667 | 1616 | Over1500 | 3.23 | 2.37 | 1.74 | 30.12 | 16.06 | 17.75 | 298391 | 225116 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EQ | LD38EQ | ld3 8eq | ld38eq | Powys | Powys | Brecon STW | 2112 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303864 | 228069 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8ER | LD38ER | ld3 8er | ld38er | Powys | Powys | Libanus WwTW | 2070 | 1534 | Over1500 | 3.07 | 2.25 | 1.65 | 28.59 | 15.25 | 16.85 | 297717 | 226205 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8ES | LD38ES | ld3 8es | ld38es | Powys | Powys | Libanus WwTW | 2694 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 298263 | 228261 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8ET | LD38ET | ld3 8et | ld38et | Powys | Powys | Libanus WwTW | 3147 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 296958 | 227427 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EU | LD38EU | ld3 8eu | ld38eu | Powys | Powys | Cradoc STW | 3525 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 297127 | 228783 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EW | LD38EW | ld3 8ew | ld38ew | Powys | Powys | Libanus WwTW | 591 | 1406 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.21 | 13.98 | 15.45 | 299366 | 225614 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EX | LD38EX | ld3 8ex | ld38ex | Powys | Powys | Llanspyddid STW | 1802 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 302879 | 228499 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8EY | LD38EY | ld3 8ey | ld38ey | Powys | Powys | Coedwaungaer STW | 3940 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 296471 | 229008 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8FB | LD38FB | ld3 8fb | ld38fb | Powys | Powys | Libanus WwTW | 345 | 1406 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.21 | 13.98 | 15.45 | 299452 | 225928 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8HA | LD38HA | ld3 8ha | ld38ha | Powys | Powys | Coedwaungaer STW | 2516 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 295005 | 228834 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8HB | LD38HB | ld3 8hb | ld38hb | Powys | Powys | Coedwaungaer STW | 2749 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 295286 | 229121 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8HD | LD38HD | ld3 8hd | ld38hd | Powys | Powys | Coedwaungaer STW | 1936 | 1279 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.84 | 12.71 | 14.05 | 294480 | 229520 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8HF | LD38HF | ld3 8hf | ld38hf | Powys | Powys | Coedwaungaer STW | 2328 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 294855 | 229704 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8HG | LD38HG | ld3 8hg | ld38hg | Powys | Powys | Coedwaungaer STW | 2003 | 1279 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.84 | 12.71 | 14.05 | 294469 | 229953 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8HH | LD38HH | ld3 8hh | ld38hh | Powys | Powys | Sennybridge Army Camp STW | 664 | 1368 | 1200to1500 | 2.74 | 2 | 1.47 | 25.5 | 13.6 | 15.03 | 293115 | 229764 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8HL | LD38HL | ld3 8hl | ld38hl | Powys | Powys | Sennybridge Army Camp STW | 925 | 1368 | 1200to1500 | 2.74 | 2 | 1.47 | 25.5 | 13.6 | 15.03 | 292769 | 230343 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8HN | LD38HN | ld3 8hn | ld38hn | Powys | Powys | Sennybridge Army Camp STW | 1584 | 1277 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.8 | 12.69 | 14.03 | 293698 | 230519 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8HP | LD38HP | ld3 8hp | ld38hp | Powys | Powys | Cradoc STW | 3881 | 1222 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.78 | 12.15 | 13.43 | 296521 | 229724 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8HR | LD38HR | ld3 8hr | ld38hr | Powys | Powys | Cradoc STW | 3439 | 1222 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.78 | 12.15 | 13.43 | 296976 | 229645 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8HS | LD38HS | ld3 8hs | ld38hs | Powys | Powys | Cradoc STW | 2915 | 1222 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.78 | 12.15 | 13.43 | 297478 | 229856 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8HT | LD38HT | ld3 8ht | ld38ht | Powys | Powys | Libanus WwTW | 424 | 1406 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.21 | 13.98 | 15.45 | 299356 | 226053 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8HW | LD38HW | ld3 8hw | ld38hw | Powys | Powys | Sennybridge Army Camp STW | 2560 | 1338 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.94 | 13.3 | 14.7 | 294825 | 230582 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8LA | LD38LA | ld3 8la | ld38la | Powys | Powys | Llanspyddid STW | 2049 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303105 | 227921 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LB | LD38LB | ld3 8lb | ld38lb | Powys | Powys | Llanspyddid STW | 2171 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 302997 | 227253 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LD | LD38LD | ld3 8ld | ld38ld | Powys | Powys | Libanus WwTW | 2087 | 1351 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.18 | 13.43 | 14.84 | 301864 | 226144 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LE | LD38LE | ld3 8le | ld38le | Powys | Powys | Libanus WwTW | 2309 | 1640 | Over1500 | 3.28 | 2.4 | 1.76 | 30.57 | 16.3 | 18.02 | 301951 | 225251 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LF | LD38LF | ld3 8lf | ld38lf | Powys | Powys | Llanspyddid STW | 2214 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 302778 | 226858 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LG | LD38LG | ld3 8lg | ld38lg | Powys | Powys | Llanspyddid STW | 2599 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 302570 | 226154 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LH | LD38LH | ld3 8lh | ld38lh | Powys | Powys | Brecon STW | 3773 | 1573 | Over1500 | 3.15 | 2.3 | 1.69 | 29.32 | 15.64 | 17.28 | 303391 | 224797 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LJ | LD38LJ | ld3 8lj | ld38lj | Powys | Powys | Llanspyddid STW | 2346 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303435 | 228239 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LL | LD38LL | ld3 8ll | ld38ll | Powys | Powys | Brecon STW | 3997 | 1708 | Over1500 | 3.42 | 2.5 | 1.83 | 31.83 | 16.98 | 18.77 | 304062 | 224058 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LN | LD38LN | ld3 8ln | ld38ln | Powys | Powys | Brecon STW | 2766 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 303953 | 225653 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LP | LD38LP | ld3 8lp | ld38lp | Powys | Powys | Llanfyrnach STW | 2735 | 1627 | Over1500 | 3.26 | 2.38 | 1.75 | 30.32 | 16.17 | 17.88 | 305735 | 224097 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LQ | LD38LQ | ld3 8lq | ld38lq | Powys | Powys | Llanspyddid STW | 1676 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 302746 | 228035 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LR | LD38LR | ld3 8lr | ld38lr | Powys | Powys | Brecon STW | 2129 | 1410 | 1200to1500 | 2.82 | 2.07 | 1.51 | 26.28 | 14.02 | 15.49 | 305603 | 225491 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LS | LD38LS | ld3 8ls | ld38ls | Powys | Powys | Brecon STW | 1319 | 1342 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.01 | 13.34 | 14.74 | 305308 | 226428 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LT | LD38LT | ld3 8lt | ld38lt | Powys | Powys | Brecon STW | 2064 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 304219 | 226428 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LU | LD38LU | ld3 8lu | ld38lu | Powys | Powys | Brecon STW | 2130 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 303802 | 227800 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8LW | LD38LW | ld3 8lw | ld38lw | Powys | Powys | Llanfyrnach STW | 2810 | 1422 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.5 | 14.14 | 15.62 | 305233 | 224810 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8NA | LD38NA | ld3 8na | ld38na | Powys | Powys | Llanspyddid STW | 1835 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 302819 | 227676 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8NB | LD38NB | ld3 8nb | ld38nb | Powys | Powys | Libanus WwTW | 1481 | 1312 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.45 | 13.04 | 14.41 | 301076 | 226751 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8ND | LD38ND | ld3 8nd | ld38nd | Powys | Powys | Libanus WwTW | 185 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 299686 | 225877 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8NE | LD38NE | ld3 8ne | ld38ne | Powys | Powys | Libanus WwTW | 1066 | 1544 | Over1500 | 3.09 | 2.26 | 1.66 | 28.78 | 15.35 | 16.96 | 300353 | 225137 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8NF | LD38NF | ld3 8nf | ld38nf | Powys | Powys | Libanus WwTW | 2954 | 1889 | Over1500 | 3.78 | 2.77 | 2.03 | 35.21 | 18.78 | 20.75 | 298279 | 223493 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8NG | LD38NG | ld3 8ng | ld38ng | Powys | Powys | Libanus WwTW | 1675 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 298692 | 224763 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8NH | LD38NH | ld3 8nh | ld38nh | Powys | Powys | Libanus WwTW | 3560 | 1889 | Over1500 | 3.78 | 2.77 | 2.03 | 35.21 | 18.78 | 20.75 | 297517 | 223289 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8NN | LD38NN | ld3 8nn | ld38nn | Powys | Powys | Libanus WwTW | 2482 | 1616 | Over1500 | 3.23 | 2.37 | 1.74 | 30.12 | 16.06 | 17.75 | 297542 | 224964 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8NP | LD38NP | ld3 8np | ld38np | Powys | Powys | Libanus WwTW | 5152 | 1783 | Over1500 | 3.57 | 2.61 | 1.91 | 33.23 | 17.72 | 19.59 | 295172 | 223735 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8NR | LD38NR | ld3 8nr | ld38nr | Powys | Powys | Libanus WwTW | 3484 | 1465 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.31 | 14.56 | 16.1 | 296318 | 226420 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8NS | LD38NS | ld3 8ns | ld38ns | Powys | Powys | Llanspyddid STW | 1478 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 299718 | 227741 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8NU | LD38NU | ld3 8nu | ld38nu | Powys | Powys | Llanspyddid STW | 2003 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 303055 | 227907 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8NW | LD38NW | ld3 8nw | ld38nw | Powys | Powys | Libanus WwTW | 4167 | 1811 | Over1500 | 3.62 | 2.65 | 1.95 | 33.75 | 18 | 19.9 | 296040 | 224200 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PA | LD38PA | ld3 8pa | ld38pa | Powys | Powys | Llanspyddid STW | 2315 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 303375 | 228659 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PB | LD38PB | ld3 8pb | ld38pb | Powys | Powys | Llanspyddid STW | 244 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 301330 | 228246 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PD | LD38PD | ld3 8pd | ld38pd | Powys | Powys | Llanspyddid STW | 238 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 301228 | 228096 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PE | LD38PE | ld3 8pe | ld38pe | Powys | Powys | Llanspyddid STW | 466 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 300933 | 227851 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PF | LD38PF | ld3 8pf | ld38pf | Powys | Powys | Llanspyddid STW | 1085 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 300019 | 228461 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PG | LD38PG | ld3 8pg | ld38pg | Powys | Powys | Coedwaungaer STW | 686 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 292214 | 228782 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PH | LD38PH | ld3 8ph | ld38ph | Powys | Powys | Coedwaungaer STW | 852 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 292080 | 228670 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PJ | LD38PJ | ld3 8pj | ld38pj | Powys | Powys | Llanspyddid STW | 175 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 301071 | 228116 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PL | LD38PL | ld3 8pl | ld38pl | Powys | Powys | Coedwaungaer STW | 1267 | 1414 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.35 | 14.06 | 15.54 | 291403 | 228843 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PN | LD38PN | ld3 8pn | ld38pn | Powys | Powys | Coedwaungaer STW | 554 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 292068 | 229108 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PP | LD38PP | ld3 8pp | ld38pp | Powys | Powys | Coedwaungaer STW | 936 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 292054 | 228586 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PR | LD38PR | ld3 8pr | ld38pr | Powys | Powys | Coedwaungaer STW | 1045 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 291939 | 228532 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PS | LD38PS | ld3 8ps | ld38ps | Powys | Powys | Coedwaungaer STW | 1128 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 291853 | 228494 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PT | LD38PT | ld3 8pt | ld38pt | Powys | Powys | Sennybridge Army Camp STW | 2219 | 1481 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.6 | 14.72 | 16.27 | 290369 | 228950 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PU | LD38PU | ld3 8pu | ld38pu | Powys | Powys | Trecastle WwTW | 1954 | 1637 | Over1500 | 3.28 | 2.4 | 1.76 | 30.51 | 16.27 | 17.99 | 289353 | 227429 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PW | LD38PW | ld3 8pw | ld38pw | Powys | Powys | Coedwaungaer STW | 875 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 292086 | 228638 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8PY | LD38PY | ld3 8py | ld38py | Powys | Powys | Cray STW | 1890 | 1796 | Over1500 | 3.59 | 2.63 | 1.93 | 33.47 | 17.85 | 19.73 | 288939 | 226077 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8RA | LD38RA | ld3 8ra | ld38ra | Powys | Powys | Cray STW | 1582 | 1796 | Over1500 | 3.59 | 2.63 | 1.93 | 33.47 | 17.85 | 19.73 | 289075 | 225800 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8RB | LD38RB | ld3 8rb | ld38rb | Powys | Powys | Trecastle WwTW | 1439 | 1497 | 1200to1500 | 3 | 2.19 | 1.61 | 27.9 | 14.88 | 16.45 | 289181 | 229712 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8RD | LD38RD | ld3 8rd | ld38rd | Powys | Powys | Trecastle WwTW | 1678 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 288411 | 230491 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8RL | LD38RL | ld3 8rl | ld38rl | Powys | Powys | Coedwaungaer STW | 761 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 292236 | 228687 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8RP | LD38RP | ld3 8rp | ld38rp | Powys | Powys | Coedwaungaer STW | 348 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 292885 | 229287 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8RR | LD38RR | ld3 8rr | ld38rr | Powys | Powys | Coedwaungaer STW | 523 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 292419 | 228874 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8RS | LD38RS | ld3 8rs | ld38rs | Powys | Powys | Coedwaungaer STW | 740 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 292254 | 228702 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8RT | LD38RT | ld3 8rt | ld38rt | Powys | Powys | Coedwaungaer STW | 938 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 292284 | 228481 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8RU | LD38RU | ld3 8ru | ld38ru | Powys | Powys | Coedwaungaer STW | 1007 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 292351 | 228393 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8RY | LD38RY | ld3 8ry | ld38ry | Powys | Powys | Coedwaungaer STW | 1085 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 292446 | 228300 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SA | LD38SA | ld3 8sa | ld38sa | Powys | Powys | Coedwaungaer STW | 1577 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 292231 | 227836 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SB | LD38SB | ld3 8sb | ld38sb | Powys | Powys | Coedwaungaer STW | 1329 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 292526 | 228052 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SD | LD38SD | ld3 8sd | ld38sd | Powys | Powys | Coedwaungaer STW | 1420 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 292564 | 227960 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SE | LD38SE | ld3 8se | ld38se | Powys | Powys | Coedwaungaer STW | 1536 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 292546 | 227844 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SF | LD38SF | ld3 8sf | ld38sf | Powys | Powys | Coedwaungaer STW | 1708 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 292583 | 227673 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SG | LD38SG | ld3 8sg | ld38sg | Powys | Powys | Coedwaungaer STW | 1755 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 292585 | 227626 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SH | LD38SH | ld3 8sh | ld38sh | Powys | Powys | Coedwaungaer STW | 1478 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 292612 | 227904 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SL | LD38SL | ld3 8sl | ld38sl | Powys | Powys | Coedwaungaer STW | 1671 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 292620 | 227711 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SN | LD38SN | ld3 8sn | ld38sn | Powys | Powys | Coedwaungaer STW | 1705 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 292668 | 227680 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SP | LD38SP | ld3 8sp | ld38sp | Powys | Powys | Coedwaungaer STW | 2630 | 1569 | Over1500 | 3.14 | 2.3 | 1.69 | 29.24 | 15.6 | 17.24 | 293041 | 226797 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SR | LD38SR | ld3 8sr | ld38sr | Powys | Powys | Coedwaungaer STW | 3062 | 1575 | Over1500 | 3.15 | 2.31 | 1.69 | 29.36 | 15.66 | 17.3 | 293656 | 226526 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SS | LD38SS | ld3 8ss | ld38ss | Powys | Powys | Cray STW | 3780 | 1712 | Over1500 | 3.43 | 2.51 | 1.84 | 31.91 | 17.02 | 18.81 | 293416 | 225289 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8ST | LD38ST | ld3 8st | ld38st | Powys | Powys | Cray STW | 2619 | 1721 | Over1500 | 3.44 | 2.52 | 1.85 | 32.08 | 17.11 | 18.91 | 292359 | 224595 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SU | LD38SU | ld3 8su | ld38su | Powys | Powys | Cray STW | 3498 | 2011 | Over1500 | 4.03 | 2.95 | 2.16 | 37.48 | 19.99 | 22.09 | 292569 | 222301 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SW | LD38SW | ld3 8sw | ld38sw | Powys | Powys | Coedwaungaer STW | 1748 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 292772 | 227647 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8SY | LD38SY | ld3 8sy | ld38sy | Powys | Powys | Cray STW | 1800 | 2055 | Over1500 | 4.11 | 3.01 | 2.21 | 38.3 | 20.43 | 22.58 | 290745 | 222871 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TA | LD38TA | ld3 8ta | ld38ta | Powys | Powys | Cray STW | 4390 | 1882 | Over1500 | 3.77 | 2.76 | 2.02 | 35.08 | 18.71 | 20.68 | 294016 | 223338 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TB | LD38TB | ld3 8tb | ld38tb | Powys | Powys | Coedwaungaer STW | 2019 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 294041 | 228019 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TD | LD38TD | ld3 8td | ld38td | Powys | Powys | Coedwaungaer STW | 3114 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 295053 | 227529 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TE | LD38TE | ld3 8te | ld38te | Powys | Powys | Coedwaungaer STW | 3974 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 295235 | 226452 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TF | LD38TF | ld3 8tf | ld38tf | Powys | Powys | Coedwaungaer STW | 3547 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 296062 | 228891 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TG | LD38TG | ld3 8tg | ld38tg | Powys | Powys | Coedwaungaer STW | 4354 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 294585 | 225532 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TL | LD38TL | ld3 8tl | ld38tl | Powys | Powys | Cray STW | 1528 | 1754 | Over1500 | 3.51 | 2.57 | 1.88 | 32.69 | 17.44 | 19.27 | 291192 | 224873 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TN | LD38TN | ld3 8tn | ld38tn | Powys | Powys | Coedwaungaer STW | 588 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 292315 | 228841 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TP | LD38TP | ld3 8tp | ld38tp | Powys | Powys | Coedwaungaer STW | 247 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 292584 | 229135 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TR | LD38TR | ld3 8tr | ld38tr | Powys | Powys | Coedwaungaer STW | 177 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 292630 | 229222 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TS | LD38TS | ld3 8ts | ld38ts | Powys | Powys | Sennybridge Army Camp STW | 176 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 292360 | 229403 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TT | LD38TT | ld3 8tt | ld38tt | Powys | Powys | Sennybridge Army Camp STW | 1111 | 1398 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.06 | 13.9 | 15.36 | 291927 | 230383 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8TU | LD38TU | ld3 8tu | ld38tu | Powys | Powys | Sennybridge Army Camp STW | 2180 | 1422 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.5 | 14.14 | 15.62 | 291017 | 231019 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8TW | LD38TW | ld3 8tw | ld38tw | Powys | Powys | Coedwaungaer STW | 293 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 292504 | 229091 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8TY | LD38TY | ld3 8ty | ld38ty | Powys | Powys | Trecastle WwTW | 2295 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 289914 | 230157 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8UA | LD38UA | ld3 8ua | ld38ua | Powys | Powys | Llanfihangle Nant Bran STW | 2621 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 292638 | 232192 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8UB | LD38UB | ld3 8ub | ld38ub | Powys | Powys | Llanfihangle Nant Bran STW | 3526 | 1403 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.15 | 13.95 | 15.41 | 291117 | 232817 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8UD | LD38UD | ld3 8ud | ld38ud | Powys | Powys | Llanfihangle Nant Bran STW | 4135 | 1486 | 1200to1500 | 2.97 | 2.18 | 1.6 | 27.7 | 14.77 | 16.33 | 290246 | 234099 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 8UE | LD38UE | ld3 8ue | ld38ue | Powys | Powys | Trecastle WwTW | 252 | 1572 | Over1500 | 3.15 | 2.3 | 1.69 | 29.3 | 15.63 | 17.27 | 288148 | 229077 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8UF | LD38UF | ld3 8uf | ld38uf | Powys | Powys | Trecastle WwTW | 241 | 1572 | Over1500 | 3.15 | 2.3 | 1.69 | 29.3 | 15.63 | 17.27 | 288081 | 229093 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8UG | LD38UG | ld3 8ug | ld38ug | Powys | Powys | Trecastle WwTW | 183 | 1572 | Over1500 | 3.15 | 2.3 | 1.69 | 29.3 | 15.63 | 17.27 | 288039 | 229041 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8UH | LD38UH | ld3 8uh | ld38uh | Powys | Powys | Trecastle WwTW | 380 | 1572 | Over1500 | 3.15 | 2.3 | 1.69 | 29.3 | 15.63 | 17.27 | 287814 | 229177 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8UL | LD38UL | ld3 8ul | ld38ul | Powys | Powys | Trecastle WwTW | 478 | 1572 | Over1500 | 3.15 | 2.3 | 1.69 | 29.3 | 15.63 | 17.27 | 287806 | 229285 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8UP | LD38UP | ld3 8up | ld38up | Powys | Powys | Trecastle WwTW | 332 | 1572 | Over1500 | 3.15 | 2.3 | 1.69 | 29.3 | 15.63 | 17.27 | 288037 | 229191 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8UQ | LD38UQ | ld3 8uq | ld38uq | Powys | Powys | Trecastle WwTW | 424 | 1572 | Over1500 | 3.15 | 2.3 | 1.69 | 29.3 | 15.63 | 17.27 | 287857 | 229250 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8UR | LD38UR | ld3 8ur | ld38ur | Powys | Powys | Trecastle WwTW | 480 | 1676 | Over1500 | 3.35 | 2.45 | 1.8 | 31.24 | 16.66 | 18.41 | 288063 | 228381 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8UT | LD38UT | ld3 8ut | ld38ut | Powys | Powys | Trecastle WwTW | 902 | 1580 | Over1500 | 3.16 | 2.31 | 1.7 | 29.45 | 15.71 | 17.36 | 288732 | 228303 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8UU | LD38UU | ld3 8uu | ld38uu | Powys | Powys | Trecastle WwTW | 1776 | 1481 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.6 | 14.72 | 16.27 | 289788 | 228672 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8UW | LD38UW | ld3 8uw | ld38uw | Powys | Powys | Trecastle WwTW | 443 | 1572 | Over1500 | 3.15 | 2.3 | 1.69 | 29.3 | 15.63 | 17.27 | 287949 | 229296 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8UY | LD38UY | ld3 8uy | ld38uy | Powys | Powys | Trecastle WwTW | 2534 | 1807 | Over1500 | 3.62 | 2.65 | 1.94 | 33.68 | 17.96 | 19.85 | 286602 | 226761 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YA | LD38YA | ld3 8ya | ld38ya | Powys | Powys | Cray STW | 2634 | 1944 | Over1500 | 3.89 | 2.85 | 2.09 | 36.23 | 19.32 | 21.36 | 287205 | 225047 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YB | LD38YB | ld3 8yb | ld38yb | Powys | Powys | Cray STW | 2271 | 1906 | Over1500 | 3.81 | 2.79 | 2.05 | 35.52 | 18.95 | 20.94 | 287856 | 225622 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YD | LD38YD | ld3 8yd | ld38yd | Powys | Powys | Trecastle WwTW | 4262 | 1924 | Over1500 | 3.85 | 2.82 | 2.07 | 35.86 | 19.13 | 21.14 | 285148 | 225713 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YE | LD38YE | ld3 8ye | ld38ye | Powys | Powys | Trecastle WwTW | 2381 | 1757 | Over1500 | 3.52 | 2.57 | 1.89 | 32.75 | 17.47 | 19.3 | 286060 | 227511 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YF | LD38YF | ld3 8yf | ld38yf | Powys | Powys | Trecastle WwTW | 3281 | 1711 | Over1500 | 3.42 | 2.51 | 1.84 | 31.89 | 17.01 | 18.8 | 284742 | 228870 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YG | LD38YG | ld3 8yg | ld38yg | Powys | Powys | Trecastle WwTW | 3999 | 1750 | Over1500 | 3.5 | 2.56 | 1.88 | 32.62 | 17.4 | 19.23 | 284524 | 226922 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YH | LD38YH | ld3 8yh | ld38yh | Powys | Powys | Coedwaungaer STW | 2016 | 1575 | Over1500 | 3.15 | 2.31 | 1.69 | 29.36 | 15.66 | 17.3 | 292164 | 227402 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YL | LD38YL | ld3 8yl | ld38yl | Powys | Powys | Cray STW | 1193 | 1754 | Over1500 | 3.51 | 2.57 | 1.88 | 32.69 | 17.44 | 19.27 | 290801 | 224934 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YN | LD38YN | ld3 8yn | ld38yn | Powys | Powys | Cray STW | 199 | 1889 | Over1500 | 3.78 | 2.77 | 2.03 | 35.21 | 18.78 | 20.75 | 289621 | 224218 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YP | LD38YP | ld3 8yp | ld38yp | Powys | Powys | Cray STW | 233 | 1889 | Over1500 | 3.78 | 2.77 | 2.03 | 35.21 | 18.78 | 20.75 | 289555 | 224498 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YR | LD38YR | ld3 8yr | ld38yr | Powys | Powys | Cray STW | 1986 | 2119 | Over1500 | 4.24 | 3.1 | 2.28 | 39.49 | 21.06 | 23.28 | 288241 | 223080 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YS | LD38YS | ld3 8ys | ld38ys | Powys | Powys | Cray STW | 2557 | 2024 | Over1500 | 4.05 | 2.96 | 2.17 | 37.72 | 20.12 | 22.24 | 287273 | 223737 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YT | LD38YT | ld3 8yt | ld38yt | Powys | Powys | Cray STW | 1590 | 1944 | Over1500 | 3.89 | 2.85 | 2.09 | 36.23 | 19.32 | 21.36 | 288174 | 224574 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YU | LD38YU | ld3 8yu | ld38yu | Powys | Powys | Cray STW | 714 | 1778 | Over1500 | 3.56 | 2.6 | 1.91 | 33.14 | 17.67 | 19.53 | 289581 | 225064 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YW | LD38YW | ld3 8yw | ld38yw | Powys | Powys | Cray STW | 171 | 1889 | Over1500 | 3.78 | 2.77 | 2.03 | 35.21 | 18.78 | 20.75 | 289593 | 224302 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8YY | LD38YY | ld3 8yy | ld38yy | Powys | Powys | Cray STW | 2880 | 2253 | Over1500 | 4.51 | 3.3 | 2.42 | 41.99 | 22.4 | 24.75 | 288941 | 221607 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AA | LD39AA | ld3 9aa | ld39aa | Powys | Powys | Brecon STW | 1789 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304386 | 228513 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AB | LD39AB | ld3 9ab | ld39ab | Powys | Powys | Brecon STW | 1819 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304379 | 228559 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AD | LD39AD | ld3 9ad | ld39ad | Powys | Powys | Brecon STW | 1823 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304397 | 228595 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AE | LD39AE | ld3 9ae | ld39ae | Powys | Powys | Brecon STW | 1829 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304414 | 228630 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AF | LD39AF | ld3 9af | ld39af | Powys | Powys | Brecon STW | 1857 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304377 | 228625 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AH | LD39AH | ld3 9ah | ld39ah | Powys | Powys | Brecon STW | 1872 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304374 | 228648 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AJ | LD39AJ | ld3 9aj | ld39aj | Powys | Powys | Llanddew STW | 419 | 1052 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.61 | 10.46 | 11.56 | 305471 | 230587 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9AL | LD39AL | ld3 9al | ld39al | Powys | Powys | Brecon STW | 1865 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304350 | 228600 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AN | LD39AN | ld3 9an | ld39an | Powys | Powys | Brecon STW | 1909 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304327 | 228644 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AP | LD39AP | ld3 9ap | ld39ap | Powys | Powys | Brecon STW | 2134 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304141 | 228771 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AQ | LD39AQ | ld3 9aq | ld39aq | Powys | Powys | Brecon STW | 1525 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305124 | 228895 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AR | LD39AR | ld3 9ar | ld39ar | Powys | Powys | Brecon STW | 2065 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304207 | 228746 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AS | LD39AS | ld3 9as | ld39as | Powys | Powys | Brecon STW | 2212 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304068 | 228802 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AT | LD39AT | ld3 9at | ld39at | Powys | Powys | Brecon STW | 2096 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304190 | 228775 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AU | LD39AU | ld3 9au | ld39au | Powys | Powys | Brecon STW | 2125 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304160 | 228784 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AX | LD39AX | ld3 9ax | ld39ax | Powys | Powys | Llanddew STW | 1959 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303732 | 229458 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9AY | LD39AY | ld3 9ay | ld39ay | Powys | Powys | Brecon STW | 2095 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304160 | 228729 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BA | LD39BA | ld3 9ba | ld39ba | Powys | Powys | Llanddew STW | 2234 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304030 | 228886 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BB | LD39BB | ld3 9bb | ld39bb | Powys | Powys | Brecon STW | 2183 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304133 | 228847 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BD | LD39BD | ld3 9bd | ld39bd | Powys | Powys | Brecon STW | 2198 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304122 | 228857 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BE | LD39BE | ld3 9be | ld39be | Powys | Powys | Brecon STW | 2118 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304236 | 228877 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BG | LD39BG | ld3 9bg | ld39bg | Powys | Powys | Brecon STW | 2130 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304186 | 228830 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BH | LD39BH | ld3 9bh | ld39bh | Powys | Powys | Brecon STW | 2139 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304176 | 228831 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BL | LD39BL | ld3 9bl | ld39bl | Powys | Powys | Llanddew STW | 2194 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304111 | 228888 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BN | LD39BN | ld3 9bn | ld39bn | Powys | Powys | Brecon STW | 2154 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304187 | 228872 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BP | LD39BP | ld3 9bp | ld39bp | Powys | Powys | Llanddew STW | 1411 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 304653 | 229502 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BQ | LD39BQ | ld3 9bq | ld39bq | Powys | Powys | Llanddew STW | 1243 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 304733 | 229653 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BR | LD39BR | ld3 9br | ld39br | Powys | Powys | Llanddew STW | 1292 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 304584 | 229660 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BS | LD39BS | ld3 9bs | ld39bs | Powys | Powys | Llanddew STW | 1331 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 304433 | 229697 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BT | LD39BT | ld3 9bt | ld39bt | Powys | Powys | Llanddew STW | 1512 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 304303 | 229565 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BU | LD39BU | ld3 9bu | ld39bu | Powys | Powys | Brecon STW | 1900 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304404 | 228738 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9BW | LD39BW | ld3 9bw | ld39bw | Powys | Powys | Brecon STW | 2156 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304150 | 228824 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DA | LD39DA | ld3 9da | ld39da | Powys | Powys | Brecon STW | 1884 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304388 | 228689 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DB | LD39DB | ld3 9db | ld39db | Powys | Powys | Brecon STW | 1995 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304282 | 228731 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DD | LD39DD | ld3 9dd | ld39dd | Powys | Powys | Brecon STW | 1870 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304428 | 228720 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DE | LD39DE | ld3 9de | ld39de | Powys | Powys | Brecon STW | 1979 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304319 | 228756 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DF | LD39DF | ld3 9df | ld39df | Powys | Powys | Brecon STW | 1982 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304379 | 228839 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DG | LD39DG | ld3 9dg | ld39dg | Powys | Powys | Brecon STW | 1965 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304406 | 228846 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DH | LD39DH | ld3 9dh | ld39dh | Powys | Powys | Brecon STW | 1966 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304454 | 228903 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DJ | LD39DJ | ld3 9dj | ld39dj | Powys | Powys | Brecon STW | 2063 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304242 | 228792 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DL | LD39DL | ld3 9dl | ld39dl | Powys | Powys | Brecon STW | 2050 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304361 | 228924 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DN | LD39DN | ld3 9dn | ld39dn | Powys | Powys | Llanddew STW | 2005 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304358 | 228980 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DP | LD39DP | ld3 9dp | ld39dp | Powys | Powys | Llanddew STW | 2003 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304416 | 228959 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DR | LD39DR | ld3 9dr | ld39dr | Powys | Powys | Llanddew STW | 2030 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304314 | 228972 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DS | LD39DS | ld3 9ds | ld39ds | Powys | Powys | Brecon STW | 2057 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304327 | 228895 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DT | LD39DT | ld3 9dt | ld39dt | Powys | Powys | Brecon STW | 2098 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304269 | 228888 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DU | LD39DU | ld3 9du | ld39du | Powys | Powys | Llanddew STW | 2124 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304223 | 228910 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DW | LD39DW | ld3 9dw | ld39dw | Powys | Powys | Llanddew STW | 1979 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304349 | 229012 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DX | LD39DX | ld3 9dx | ld39dx | Powys | Powys | Llanddew STW | 2026 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304348 | 228962 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9DY | LD39DY | ld3 9dy | ld39dy | Powys | Powys | Llanddew STW | 2106 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304218 | 228932 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EA | LD39EA | ld3 9ea | ld39ea | Powys | Powys | Llanddew STW | 1792 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304317 | 229234 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EB | LD39EB | ld3 9eb | ld39eb | Powys | Powys | Llanddew STW | 1956 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304335 | 229044 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9ED | LD39ED | ld3 9ed | ld39ed | Powys | Powys | Llanddew STW | 1846 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304417 | 229128 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EE | LD39EE | ld3 9ee | ld39ee | Powys | Powys | Brecon STW | 1828 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304430 | 228652 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EF | LD39EF | ld3 9ef | ld39ef | Powys | Powys | Llanddew STW | 1903 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304299 | 229119 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EG | LD39EG | ld3 9eg | ld39eg | Powys | Powys | Llanddew STW | 1862 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304256 | 229186 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EH | LD39EH | ld3 9eh | ld39eh | Powys | Powys | Llanddew STW | 1625 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304345 | 229408 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EL | LD39EL | ld3 9el | ld39el | Powys | Powys | Llanddew STW | 1563 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304334 | 229485 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EN | LD39EN | ld3 9en | ld39en | Powys | Powys | Llanddew STW | 1656 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304417 | 229336 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EP | LD39EP | ld3 9ep | ld39ep | Powys | Powys | Llanddew STW | 1657 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304546 | 229280 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EQ | LD39EQ | ld3 9eq | ld39eq | Powys | Powys | Llanddew STW | 1484 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304729 | 229402 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9ER | LD39ER | ld3 9er | ld39er | Powys | Powys | Llanddew STW | 1434 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 304449 | 229569 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9ES | LD39ES | ld3 9es | ld39es | Powys | Powys | Llanddew STW | 1506 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304499 | 229463 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9ET | LD39ET | ld3 9et | ld39et | Powys | Powys | Llanddew STW | 1505 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304661 | 229400 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EU | LD39EU | ld3 9eu | ld39eu | Powys | Powys | Llanddew STW | 1836 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304473 | 229116 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EW | LD39EW | ld3 9ew | ld39ew | Powys | Powys | Llanddew STW | 1760 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304446 | 229209 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9EY | LD39EY | ld3 9ey | ld39ey | Powys | Powys | Llanddew STW | 1472 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304663 | 229434 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HA | LD39HA | ld3 9ha | ld39ha | Powys | Powys | Llanddew STW | 2223 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303960 | 228941 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HB | LD39HB | ld3 9hb | ld39hb | Powys | Powys | Llanddew STW | 2124 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304103 | 228972 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HD | LD39HD | ld3 9hd | ld39hd | Powys | Powys | Llanddew STW | 2141 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304153 | 228926 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HE | LD39HE | ld3 9he | ld39he | Powys | Powys | Llanddew STW | 2055 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304248 | 228975 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HF | LD39HF | ld3 9hf | ld39hf | Powys | Powys | Llanddew STW | 2073 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304197 | 228980 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HG | LD39HG | ld3 9hg | ld39hg | Powys | Powys | Llanddew STW | 1971 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304253 | 229066 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HH | LD39HH | ld3 9hh | ld39hh | Powys | Powys | Llanddew STW | 2044 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304166 | 229028 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HJ | LD39HJ | ld3 9hj | ld39hj | Powys | Powys | Llanddew STW | 1795 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304255 | 229263 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HL | LD39HL | ld3 9hl | ld39hl | Powys | Powys | Llanddew STW | 1993 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304132 | 229105 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HN | LD39HN | ld3 9hn | ld39hn | Powys | Powys | Llanddew STW | 1940 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304233 | 229110 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HP | LD39HP | ld3 9hp | ld39hp | Powys | Powys | Llanddew STW | 1994 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304035 | 229164 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HR | LD39HR | ld3 9hr | ld39hr | Powys | Powys | Llanddew STW | 1953 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304010 | 229231 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HS | LD39HS | ld3 9hs | ld39hs | Powys | Powys | Llanddew STW | 1813 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304205 | 229271 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HT | LD39HT | ld3 9ht | ld39ht | Powys | Powys | Llanddew STW | 1847 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304107 | 229293 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HU | LD39HU | ld3 9hu | ld39hu | Powys | Powys | Llanddew STW | 1812 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304062 | 229367 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HW | LD39HW | ld3 9hw | ld39hw | Powys | Powys | Llanddew STW | 1928 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304153 | 229169 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9HY | LD39HY | ld3 9hy | ld39hy | Powys | Powys | Llanddew STW | 1927 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303989 | 229278 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9LA | LD39LA | ld3 9la | ld39la | Powys | Powys | Llanddew STW | 2132 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304184 | 228920 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9LB | LD39LB | ld3 9lb | ld39lb | Powys | Powys | Brecon STW | 2137 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304207 | 228871 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9LD | LD39LD | ld3 9ld | ld39ld | Powys | Powys | Llanddew STW | 1743 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304174 | 229373 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9LE | LD39LE | ld3 9le | ld39le | Powys | Powys | Llanddew STW | 1744 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304021 | 229485 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9LF | LD39LF | ld3 9lf | ld39lf | Powys | Powys | Llanddew STW | 1794 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303936 | 229492 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9LG | LD39LG | ld3 9lg | ld39lg | Powys | Powys | Llanddew STW | 2144 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 304011 | 229002 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9LH | LD39LH | ld3 9lh | ld39lh | Powys | Powys | Llanddew STW | 2104 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303892 | 229130 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9LL | LD39LL | ld3 9ll | ld39ll | Powys | Powys | Llanddew STW | 2205 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303916 | 228990 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9LN | LD39LN | ld3 9ln | ld39ln | Powys | Powys | Llanddew STW | 911 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 304290 | 230477 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9LP | LD39LP | ld3 9lp | ld39lp | Powys | Powys | Cradoc STW | 1830 | 1159 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.6 | 11.52 | 12.73 | 302072 | 230833 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9LR | LD39LR | ld3 9lr | ld39lr | Powys | Powys | Cradoc STW | 1333 | 1159 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.6 | 11.52 | 12.73 | 301617 | 230634 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9LS | LD39LS | ld3 9ls | ld39ls | Powys | Powys | Cradoc STW | 2018 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 298393 | 230503 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9LT | LD39LT | ld3 9lt | ld39lt | Powys | Powys | Pontfaen STW | 3245 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 297145 | 232038 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9LU | LD39LU | ld3 9lu | ld39lu | Powys | Powys | Llanfihangle Nant Bran STW | 1623 | 1344 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.05 | 13.36 | 14.77 | 295059 | 232676 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9LW | LD39LW | ld3 9lw | ld39lw | Powys | Powys | Cradoc STW | 1871 | 1159 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.6 | 11.52 | 12.73 | 302141 | 230767 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9LY | LD39LY | ld3 9ly | ld39ly | Powys | Powys | Llanfihangle Nant Bran STW | 1571 | 1239 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.09 | 12.32 | 13.61 | 295766 | 233411 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9NA | LD39NA | ld3 9na | ld39na | Powys | Powys | Llanfihangle Nant Bran STW | 166 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 294421 | 234311 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9NB | LD39NB | ld3 9nb | ld39nb | Powys | Powys | Llanfihangle Nant Bran STW | 1655 | 1312 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.45 | 13.04 | 14.41 | 293812 | 235704 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9ND | LD39ND | ld3 9nd | ld39nd | Powys | Powys | Pontfaen STW | 1501 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 298165 | 233887 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9NE | LD39NE | ld3 9ne | ld39ne | Powys | Powys | Pontfaen STW | 896 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 299136 | 233366 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9NF | LD39NF | ld3 9nf | ld39nf | Powys | Powys | Cradoc STW | 1310 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 299870 | 231349 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9NG | LD39NG | ld3 9ng | ld39ng | Powys | Powys | Cradoc STW | 1912 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 298671 | 229281 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9NH | LD39NH | ld3 9nh | ld39nh | Powys | Powys | Cradoc STW | 2041 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 298415 | 229586 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9NL | LD39NL | ld3 9nl | ld39nl | Powys | Powys | Cradoc STW | 2922 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 297488 | 230569 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9NN | LD39NN | ld3 9nn | ld39nn | Powys | Powys | Cradoc STW | 2049 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 298341 | 229922 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9NP | LD39NP | ld3 9np | ld39np | Powys | Powys | Cradoc STW | 353 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 300293 | 230485 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9NR | LD39NR | ld3 9nr | ld39nr | Powys | Powys | Cradoc STW | 1371 | 1206 | 1200to1500 | 2.41 | 1.77 | 1.3 | 22.48 | 11.99 | 13.25 | 299420 | 231122 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9NS | LD39NS | ld3 9ns | ld39ns | Powys | Powys | Cradoc STW | 941 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 300091 | 231038 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9NT | LD39NT | ld3 9nt | ld39nt | Powys | Powys | Cradoc STW | 300 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 300402 | 229843 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9NU | LD39NU | ld3 9nu | ld39nu | Powys | Powys | Cradoc STW | 498 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 300466 | 230632 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9NW | LD39NW | ld3 9nw | ld39nw | Powys | Powys | Cradoc STW | 539 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 299920 | 229858 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9NY | LD39NY | ld3 9ny | ld39ny | Powys | Powys | Cradoc STW | 759 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 301062 | 230471 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9PA | LD39PA | ld3 9pa | ld39pa | Powys | Powys | Cradoc STW | 1381 | 1129 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.04 | 11.22 | 12.4 | 301721 | 229824 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9PB | LD39PB | ld3 9pb | ld39pb | Powys | Powys | Cradoc STW | 1308 | 1159 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.6 | 11.52 | 12.73 | 301627 | 230529 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9PD | LD39PD | ld3 9pd | ld39pd | Powys | Powys | Cradoc STW | 1445 | 1159 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.6 | 11.52 | 12.73 | 301733 | 230643 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9PE | LD39PE | ld3 9pe | ld39pe | Powys | Powys | Cradoc STW | 1878 | 1129 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.04 | 11.22 | 12.4 | 302255 | 230147 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9PF | LD39PF | ld3 9pf | ld39pf | Powys | Powys | Llanddew STW | 2146 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303565 | 229362 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9PG | LD39PG | ld3 9pg | ld39pg | Powys | Powys | Llanspyddid STW | 2462 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 303452 | 228983 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9PH | LD39PH | ld3 9ph | ld39ph | Powys | Powys | Llanspyddid STW | 1160 | 1113 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.74 | 11.06 | 12.23 | 302043 | 228950 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9PL | LD39PL | ld3 9pl | ld39pl | Powys | Powys | Llanddew STW | 1646 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 304151 | 229507 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9PN | LD39PN | ld3 9pn | ld39pn | Powys | Powys | Llanddew STW | 1704 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 304011 | 229546 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9PP | LD39PP | ld3 9pp | ld39pp | Powys | Powys | Llanddew STW | 2375 | 1141 | 900to1200 | 2.28 | 1.67 | 1.23 | 21.27 | 11.34 | 12.54 | 303041 | 231958 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9PR | LD39PR | ld3 9pr | ld39pr | Powys | Powys | STW At Lower Chapel Brecon , | 2898 | 1129 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.04 | 11.22 | 12.4 | 302980 | 232843 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9PS | LD39PS | ld3 9ps | ld39ps | Powys | Powys | Llanddew STW | 2503 | 1129 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.04 | 11.22 | 12.4 | 303330 | 232568 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9PT | LD39PT | ld3 9pt | ld39pt | Powys | Powys | STW At Lower Chapel Brecon , | 3097 | 1129 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.04 | 11.22 | 12.4 | 302601 | 232637 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9PU | LD39PU | ld3 9pu | ld39pu | Powys | Powys | STW At Lower Chapel Brecon , | 2377 | 1129 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.04 | 11.22 | 12.4 | 303001 | 233368 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9PW | LD39PW | ld3 9pw | ld39pw | Powys | Powys | STW At Lower Chapel Brecon , | 1997 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 303125 | 233771 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9PY | LD39PY | ld3 9py | ld39py | Powys | Powys | STW At Lower Chapel Brecon , | 2126 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 303148 | 233644 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9QA | LD39QA | ld3 9qa | ld39qa | Powys | Powys | Cradoc STW | 1311 | 1129 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.04 | 11.22 | 12.4 | 301650 | 230459 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9RA | LD39RA | ld3 9ra | ld39ra | Powys | Powys | STW At Lower Chapel Brecon , | 2051 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 303157 | 233722 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RB | LD39RB | ld3 9rb | ld39rb | Powys | Powys | STW At Lower Chapel Brecon , | 1711 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 303079 | 234053 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RD | LD39RD | ld3 9rd | ld39rd | Powys | Powys | STW At Lower Chapel Brecon , | 1025 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 302890 | 234716 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RE | LD39RE | ld3 9re | ld39re | Powys | Powys | STW At Lower Chapel Brecon , | 305 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 303034 | 235812 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RF | LD39RF | ld3 9rf | ld39rf | Powys | Powys | STW At Lower Chapel Brecon , | 1370 | 1222 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.78 | 12.15 | 13.43 | 302395 | 237055 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RG | LD39RG | ld3 9rg | ld39rg | Powys | Powys | STW At Lower Chapel Brecon , | 5217 | 1284 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.93 | 12.76 | 14.11 | 300792 | 240568 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RH | LD39RH | ld3 9rh | ld39rh | Powys | Powys | STW At Lower Chapel Brecon , | 207 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 302840 | 235911 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RL | LD39RL | ld3 9rl | ld39rl | Powys | Powys | Llanddew STW | 568 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 305689 | 230932 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RN | LD39RN | ld3 9rn | ld39rn | Powys | Powys | Cradoc STW | 980 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 300880 | 230983 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RP | LD39RP | ld3 9rp | ld39rp | Powys | Powys | Pontfaen STW | 850 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 300477 | 234294 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RR | LD39RR | ld3 9rr | ld39rr | Powys | Powys | Pontfaen STW | 44 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 299617 | 234071 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RS | LD39RS | ld3 9rs | ld39rs | Powys | Powys | Pontfaen STW | 514 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 299762 | 234602 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RT | LD39RT | ld3 9rt | ld39rt | Powys | Powys | Pontfaen STW | 1170 | 1240 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.11 | 12.33 | 13.62 | 298886 | 234986 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RU | LD39RU | ld3 9ru | ld39ru | Powys | Powys | Pontfaen STW | 2594 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 297217 | 234997 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RW | LD39RW | ld3 9rw | ld39rw | Powys | Powys | Pontfaen STW | 1795 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 300267 | 232415 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9RY | LD39RY | ld3 9ry | ld39ry | Powys | Powys | Pontfaen STW | 1074 | 1240 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.11 | 12.33 | 13.62 | 299384 | 235140 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SA | LD39SA | ld3 9sa | ld39sa | Powys | Powys | Pontfaen STW | 3325 | 1269 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.65 | 12.61 | 13.94 | 297580 | 236701 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SB | LD39SB | ld3 9sb | ld39sb | Powys | Powys | Llanfihangle Nant Bran STW | 4187 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 296715 | 237624 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SD | LD39SD | ld3 9sd | ld39sd | Powys | Powys | Pontfaen STW | 3611 | 1282 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.89 | 12.74 | 14.09 | 298504 | 237523 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SE | LD39SE | ld3 9se | ld39se | Powys | Powys | Pontfaen STW | 4641 | 1295 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.14 | 12.87 | 14.23 | 298523 | 238601 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SF | LD39SF | ld3 9sf | ld39sf | Powys | Powys | Pontfaen STW | 4714 | 1295 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.14 | 12.87 | 14.23 | 298939 | 238759 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SG | LD39SG | ld3 9sg | ld39sg | Powys | Powys | Pontfaen STW | 3102 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 299615 | 237201 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SH | LD39SH | ld3 9sh | ld39sh | Powys | Powys | Pontfaen STW | 1989 | 1252 | 1200to1500 | 2.51 | 1.83 | 1.34 | 23.34 | 12.45 | 13.76 | 300551 | 235873 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SN | LD39SN | ld3 9sn | ld39sn | Powys | Powys | Llanddew STW | 1105 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 305157 | 229726 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9SP | LD39SP | ld3 9sp | ld39sp | Powys | Powys | Llanddew STW | 929 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 305568 | 230011 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SR | LD39SR | ld3 9sr | ld39sr | Powys | Powys | Brecon STW | 1677 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305098 | 229056 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9SS | LD39SS | ld3 9ss | ld39ss | Powys | Powys | Llanddew STW | 436 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 305559 | 230753 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9ST | LD39ST | ld3 9st | ld39st | Powys | Powys | Llanddew STW | 350 | 1052 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.61 | 10.46 | 11.56 | 305478 | 230791 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SU | LD39SU | ld3 9su | ld39su | Powys | Powys | Llanddew STW | 479 | 1052 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.61 | 10.46 | 11.56 | 304675 | 230978 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SW | LD39SW | ld3 9sw | ld39sw | Powys | Powys | Llanddew STW | 978 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 305678 | 230020 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SX | LD39SX | ld3 9sx | ld39sx | Powys | Powys | Brecon STW | 1481 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305160 | 228865 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9SY | LD39SY | ld3 9sy | ld39sy | Powys | Powys | Llanddew STW | 534 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 305641 | 230675 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9SZ | LD39SZ | ld3 9sz | ld39sz | Powys | Powys | Brecon STW | 1544 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305178 | 228948 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9TE | LD39TE | ld3 9te | ld39te | Powys | Powys | Llanddew STW | 2614 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 306112 | 233252 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9TF | LD39TF | ld3 9tf | ld39tf | Powys | Powys | Llanddew STW | 1946 | 1078 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.09 | 10.72 | 11.84 | 306348 | 232347 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9TG | LD39TG | ld3 9tg | ld39tg | Powys | Powys | Llanddew STW | 2184 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 304871 | 232998 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9TN | LD39TN | ld3 9tn | ld39tn | Powys | Powys | STW At Lower Chapel Brecon , | 2376 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 304925 | 234799 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9TP | LD39TP | ld3 9tp | ld39tp | Powys | Powys | STW At Lower Chapel Brecon , | 2033 | 1135 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.15 | 11.28 | 12.47 | 303896 | 234058 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9TR | LD39TR | ld3 9tr | ld39tr | Powys | Powys | Llanddew STW | 1846 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 303624 | 231896 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9TS | LD39TS | ld3 9ts | ld39ts | Powys | Powys | Llanddew STW | 1233 | 1078 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.09 | 10.72 | 11.84 | 304041 | 231407 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9TT | LD39TT | ld3 9tt | ld39tt | Powys | Powys | Llanddew STW | 2341 | 1141 | 900to1200 | 2.28 | 1.67 | 1.23 | 21.27 | 11.34 | 12.54 | 303456 | 232466 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9TW | LD39TW | ld3 9tw | ld39tw | Powys | Powys | Llanddew STW | 2728 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 304882 | 233546 | Powys LPA | PO | River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council
LD3 9UA | LD39UA | ld3 9ua | ld39ua | Powys | Powys | Llanddew STW | 2079 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303705 | 229317 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9UB | LD39UB | ld3 9ub | ld39ub | Powys | Powys | Llanddew STW | 2000 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303841 | 229302 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9UD | LD39UD | ld3 9ud | ld39ud | Powys | Powys | Llanddew STW | 1899 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303867 | 229412 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9UE | LD39UE | ld3 9ue | ld39ue | Powys | Powys | Llanddew STW | 2018 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303889 | 229240 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 9UF | LD39UF | ld3 9uf | ld39uf | Powys | Powys | Llanddew STW | 1936 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 303799 | 229425 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP10 0AA | NP100AA | np10 0aa | np100aa | Newport | Casnewydd | Caerleon Road STW | 6545 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327203 | 188953 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AB | NP100AB | np10 0ab | np100ab | Newport | Casnewydd | Caerleon Road STW | 6344 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327399 | 189019 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AD | NP100AD | np10 0ad | np100ad | Newport | Casnewydd | Caerleon Road STW | 6448 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327278 | 189319 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AE | NP100AE | np10 0ae | np100ae | Newport | Casnewydd | Caerleon Road STW | 6493 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327270 | 188806 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AF | NP100AF | np10 0af | np100af | Newport | Casnewydd | Caerleon Road STW | 6764 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 326968 | 189167 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AG | NP100AG | np10 0ag | np100ag | Newport | Casnewydd | Caerleon Road STW | 6567 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327188 | 188878 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AH | NP100AH | np10 0ah | np100ah | Newport | Casnewydd | Caerleon Road STW | 6618 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327128 | 188970 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AJ | NP100AJ | np10 0aj | np100aj | Newport | Casnewydd | Caerleon Road STW | 6616 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327121 | 189092 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AL | NP100AL | np10 0al | np100al | Newport | Casnewydd | Caerleon Road STW | 6630 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327096 | 189293 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AN | NP100AN | np10 0an | np100an | Newport | Casnewydd | Caerleon Road STW | 6625 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327128 | 188897 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AP | NP100AP | np10 0ap | np100ap | Newport | Casnewydd | Caerleon Road STW | 6452 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327294 | 188973 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AQ | NP100AQ | np10 0aq | np100aq | Newport | Casnewydd | Caerleon Road STW | 6597 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327152 | 188939 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AR | NP100AR | np10 0ar | np100ar | Newport | Casnewydd | Caerleon Road STW | 6474 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327278 | 188914 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AS | NP100AS | np10 0as | np100as | Newport | Casnewydd | Caerleon Road STW | 6497 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327251 | 188953 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AT | NP100AT | np10 0at | np100at | Newport | Casnewydd | Caerleon Road STW | 6532 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327211 | 189011 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AU | NP100AU | np10 0au | np100au | Newport | Casnewydd | Caerleon Road STW | 6569 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327165 | 189142 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AW | NP100AW | np10 0aw | np100aw | Newport | Casnewydd | Caerleon Road STW | 6286 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327472 | 188855 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AX | NP100AX | np10 0ax | np100ax | Newport | Casnewydd | Caerleon Road STW | 6409 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327339 | 188960 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AY | NP100AY | np10 0ay | np100ay | Newport | Casnewydd | Caerleon Road STW | 6423 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327320 | 189015 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0AZ | NP100AZ | np10 0az | np100az | Newport | Casnewydd | Caerleon Road STW | 6458 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327281 | 189069 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BA | NP100BA | np10 0ba | np100ba | Newport | Casnewydd | Caerleon Road STW | 6708 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327030 | 189068 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BB | NP100BB | np10 0bb | np100bb | Newport | Casnewydd | Caerleon Road STW | 6691 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327052 | 189002 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BD | NP100BD | np10 0bd | np100bd | Newport | Casnewydd | Caerleon Road STW | 6435 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327295 | 189216 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BE | NP100BE | np10 0be | np100be | Newport | Casnewydd | Caerleon Road STW | 6510 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327219 | 189235 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BG | NP100BG | np10 0bg | np100bg | Newport | Casnewydd | Caerleon Road STW | 6504 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327223 | 189275 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BH | NP100BH | np10 0bh | np100bh | Newport | Casnewydd | Caerleon Road STW | 6502 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327221 | 189457 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BJ | NP100BJ | np10 0bj | np100bj | Newport | Casnewydd | Caerleon Road STW | 6310 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327452 | 188823 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BL | NP100BL | np10 0bl | np100bl | Newport | Casnewydd | Caerleon Road STW | 6448 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327275 | 189417 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BP | NP100BP | np10 0bp | np100bp | Newport | Casnewydd | Caerleon Road STW | 6321 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327462 | 188654 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BQ | NP100BQ | np10 0bq | np100bq | Newport | Casnewydd | Caerleon Road STW | 6327 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327446 | 188728 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BS | NP100BS | np10 0bs | np100bs | Newport | Casnewydd | Caerleon Road STW | 6212 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327594 | 188514 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BT | NP100BT | np10 0bt | np100bt | Newport | Casnewydd | Caerleon Road STW | 6045 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327753 | 188575 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BU | NP100BU | np10 0bu | np100bu | Newport | Casnewydd | Caerleon Road STW | 6114 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327687 | 188554 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BW | NP100BW | np10 0bw | np100bw | Newport | Casnewydd | Caerleon Road STW | 6233 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327548 | 188674 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BX | NP100BX | np10 0bx | np100bx | Newport | Casnewydd | Caerleon Road STW | 6109 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327677 | 188647 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0BY | NP100BY | np10 0by | np100by | Newport | Casnewydd | Caerleon Road STW | 6152 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327627 | 188693 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0DB | NP100DB | np10 0db | np100db | Newport | Casnewydd | Caerleon Road STW | 6150 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327617 | 188790 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0DD | NP100DD | np10 0dd | np100dd | Newport | Casnewydd | Caerleon Road STW | 6214 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327553 | 188788 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0DE | NP100DE | np10 0de | np100de | Newport | Casnewydd | Caerleon Road STW | 6217 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327555 | 188744 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0DF | NP100DF | np10 0df | np100df | Newport | Casnewydd | Caerleon Road STW | 6126 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327641 | 188786 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0DL | NP100DL | np10 0dl | np100dl | Newport | Casnewydd | Caerleon Road STW | 6059 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327718 | 188715 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0DN | NP100DN | np10 0dn | np100dn | Newport | Casnewydd | Caerleon Road STW | 6098 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327693 | 188615 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0DW | NP100DW | np10 0dw | np100dw | Newport | Casnewydd | Caerleon Road STW | 6026 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327753 | 188701 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 0ED | NP100ED | np10 0ed | np100ed | Newport | Casnewydd | Caerleon Road STW | 6634 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327105 | 189060 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 8UZ | NP108UZ | np10 8uz | np108uz | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 8XA | NP108XA | np10 8xa | np108xa | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 8YG | NP108YG | np10 8yg | np108yg | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 8YT | NP108YT | np10 8yt | np108yt | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 8YU | NP108YU | np10 8yu | np108yu | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 8ZS | NP108ZS | np10 8zs | np108zs | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AA | NP109AA | np10 9aa | np109aa | Newport | Casnewydd | Caerleon Road STW | 5767 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 328167 | 187981 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AD | NP109AD | np10 9ad | np109ad | Newport | Casnewydd | Caerleon Road STW | 5758 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 328124 | 188183 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AE | NP109AE | np10 9ae | np109ae | Newport | Casnewydd | Caerleon Road STW | 5851 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 328026 | 188191 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AF | NP109AF | np10 9af | np109af | Newport | Casnewydd | Caerleon Road STW | 5847 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 327976 | 188449 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AG | NP109AG | np10 9ag | np109ag | Newport | Casnewydd | Caerleon Road STW | 6167 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327585 | 188922 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AH | NP109AH | np10 9ah | np109ah | Newport | Casnewydd | Caerleon Road STW | 5915 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 327910 | 188432 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AJ | NP109AJ | np10 9aj | np109aj | Newport | Casnewydd | Caerleon Road STW | 5945 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 327875 | 188457 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AL | NP109AL | np10 9al | np109al | Newport | Casnewydd | Caerleon Road STW | 6008 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327801 | 188513 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AP | NP109AP | np10 9ap | np109ap | Newport | Casnewydd | Caerleon Road STW | 6094 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 327720 | 188477 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AQ | NP109AQ | np10 9aq | np109aq | Newport | Casnewydd | Caerleon Road STW | 6342 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327463 | 188511 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AR | NP109AR | np10 9ar | np109ar | Newport | Casnewydd | Caerleon Road STW | 6589 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327172 | 188812 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AS | NP109AS | np10 9as | np109as | Newport | Casnewydd | Caerleon Road STW | 6668 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327091 | 188833 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AU | NP109AU | np10 9au | np109au | Newport | Casnewydd | Caerleon Road STW | 6222 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327523 | 188997 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AW | NP109AW | np10 9aw | np109aw | Newport | Casnewydd | Caerleon Road STW | 6226 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327513 | 189069 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9AX | NP109AX | np10 9ax | np109ax | Newport | Casnewydd | Caerleon Road STW | 6322 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327414 | 189112 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9FX | NP109FX | np10 9fx | np109fx | Newport | Casnewydd | Caerleon Road STW | 6823 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 326909 | 189167 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9GN | NP109GN | np10 9gn | np109gn | Newport | Casnewydd | Caerleon Road STW | 5469 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 328269 | 189114 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9GP | NP109GP | np10 9gp | np109gp | Newport | Casnewydd | Caerleon Road STW | 6361 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327372 | 189167 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9GQ | NP109GQ | np10 9gq | np109gq | Newport | Casnewydd | Caerleon Road STW | 5922 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327850 | 188764 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9HH | NP109HH | np10 9hh | np109hh | Newport | Casnewydd | Caerleon Road STW | 6726 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327021 | 188956 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9HJ | NP109HJ | np10 9hj | np109hj | Newport | Casnewydd | Caerleon Road STW | 6158 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327578 | 189116 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9HL | NP109HL | np10 9hl | np109hl | Newport | Casnewydd | Caerleon Road STW | 6140 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327599 | 189069 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9HN | NP109HN | np10 9hn | np109hn | Newport | Casnewydd | Caerleon Road STW | 6168 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327573 | 189053 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9HP | NP109HP | np10 9hp | np109hp | Newport | Casnewydd | Caerleon Road STW | 6097 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327636 | 189165 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9HW | NP109HW | np10 9hw | np109hw | Newport | Casnewydd | Caerleon Road STW | 6241 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327485 | 189298 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9HX | NP109HX | np10 9hx | np109hx | Newport | Casnewydd | Caerleon Road STW | 6101 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 327643 | 189018 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9HY | NP109HY | np10 9hy | np109hy | Newport | Casnewydd | Caerleon Road STW | 6817 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 326923 | 189035 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9LH | NP109LH | np10 9lh | np109lh | Newport | Casnewydd | Caerleon Road STW | 6351 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327372 | 189415 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9LW | NP109LW | np10 9lw | np109lw | Newport | Casnewydd | Caerleon Road STW | 5797 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 328044 | 188362 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9LX | NP109LX | np10 9lx | np109lx | Newport | Casnewydd | Caerleon Road STW | 5753 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 328095 | 188333 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9LY | NP109LY | np10 9ly | np109ly | Newport | Casnewydd | Caerleon Road STW | 5764 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 328096 | 188275 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9SG | NP109SG | np10 9sg | np109sg | Newport | Casnewydd | Caerleon Road STW | 5668 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 328281 | 187943 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9SH | NP109SH | np10 9sh | np109sh | Newport | Casnewydd | Caerleon Road STW | 5720 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 328234 | 187919 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9SW | NP109SW | np10 9sw | np109sw | Newport | Casnewydd | Caerleon Road STW | 6342 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327392 | 189137 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9TG | NP109TG | np10 9tg | np109tg | Newport | Casnewydd | Caerleon Road STW | 5017 | 1180 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.99 | 11.73 | 12.96 | 328706 | 189400 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP10 9US | NP109US | np10 9us | np109us | Newport | Casnewydd | Caerleon Road STW | 6275 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 327448 | 189442 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP15 1AA | NP151AA | np15 1aa | np151aa | Monmouthshire | Sir Fynwy | Usk STW | 1809 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337780 | 201017 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AB | NP151AB | np15 1ab | np151ab | Monmouthshire | Sir Fynwy | Usk STW | 1716 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337672 | 200837 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AD | NP151AD | np15 1ad | np151ad | Monmouthshire | Sir Fynwy | Usk STW | 1440 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337770 | 200564 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AE | NP151AE | np15 1ae | np151ae | Monmouthshire | Sir Fynwy | Usk STW | 1572 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337726 | 200698 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AF | NP151AF | np15 1af | np151af | Monmouthshire | Sir Fynwy | Usk STW | 1182 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337907 | 200342 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AG | NP151AG | np15 1ag | np151ag | Monmouthshire | Sir Fynwy | Usk STW | 1594 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337780 | 200764 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AH | NP151AH | np15 1ah | np151ah | Monmouthshire | Sir Fynwy | Usk STW | 1217 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337856 | 200344 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AJ | NP151AJ | np15 1aj | np151aj | Monmouthshire | Sir Fynwy | Usk STW | 1518 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337798 | 200684 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AL | NP151AL | np15 1al | np151al | Monmouthshire | Sir Fynwy | Usk STW | 1511 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337674 | 200576 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AN | NP151AN | np15 1an | np151an | Monmouthshire | Sir Fynwy | Usk STW | 1466 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337637 | 200478 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AP | NP151AP | np15 1ap | np151ap | Monmouthshire | Sir Fynwy | Usk STW | 1318 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337725 | 200356 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AQ | NP151AQ | np15 1aq | np151aq | Monmouthshire | Sir Fynwy | Usk STW | 1552 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337643 | 200603 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AR | NP151AR | np15 1ar | np151ar | Monmouthshire | Sir Fynwy | Usk STW | 1428 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337694 | 200481 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AS | NP151AS | np15 1as | np151as | Monmouthshire | Sir Fynwy | Usk STW | 1515 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337576 | 200485 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AT | NP151AT | np15 1at | np151at | Monmouthshire | Sir Fynwy | Usk STW | 1696 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337508 | 200674 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AU | NP151AU | np15 1au | np151au | Monmouthshire | Sir Fynwy | Usk STW | 1631 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337566 | 200640 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AW | NP151AW | np15 1aw | np151aw | Monmouthshire | Sir Fynwy | Usk STW | 1315 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337696 | 200321 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AX | NP151AX | np15 1ax | np151ax | Monmouthshire | Sir Fynwy | Usk STW | 1623 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337788 | 200804 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AY | NP151AY | np15 1ay | np151ay | Monmouthshire | Sir Fynwy | Usk STW | 1558 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337521 | 200490 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1AZ | NP151AZ | np15 1az | np151az | Monmouthshire | Sir Fynwy | Usk STW | 1294 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337768 | 200367 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BA | NP151BA | np15 1ba | np151ba | Monmouthshire | Sir Fynwy | Usk STW | 1646 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337521 | 200617 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BB | NP151BB | np15 1bb | np151bb | Monmouthshire | Sir Fynwy | Usk STW | 1440 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337852 | 200627 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BD | NP151BD | np15 1bd | np151bd | Monmouthshire | Sir Fynwy | Usk STW | 1572 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337834 | 200773 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BE | NP151BE | np15 1be | np151be | Monmouthshire | Sir Fynwy | Usk STW | 1636 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337981 | 200927 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BG | NP151BG | np15 1bg | np151bg | Monmouthshire | Sir Fynwy | Usk STW | 1784 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337553 | 200831 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BH | NP151BH | np15 1bh | np151bh | Monmouthshire | Sir Fynwy | Usk STW | 1750 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337777 | 200947 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BJ | NP151BJ | np15 1bj | np151bj | Monmouthshire | Sir Fynwy | Usk STW | 1693 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337757 | 200867 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BL | NP151BL | np15 1bl | np151bl | Monmouthshire | Sir Fynwy | Usk STW | 1593 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338116 | 200938 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BN | NP151BN | np15 1bn | np151bn | Monmouthshire | Sir Fynwy | Usk STW | 1634 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337957 | 200914 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BP | NP151BP | np15 1bp | np151bp | Monmouthshire | Sir Fynwy | Usk STW | 1662 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338118 | 201013 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BQ | NP151BQ | np15 1bq | np151bq | Monmouthshire | Sir Fynwy | Usk STW | 1761 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337573 | 200818 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BR | NP151BR | np15 1br | np151br | Monmouthshire | Sir Fynwy | Usk STW | 1633 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337792 | 200819 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BS | NP151BS | np15 1bs | np151bs | Monmouthshire | Sir Fynwy | Usk STW | 1704 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338104 | 201052 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BT | NP151BT | np15 1bt | np151bt | Monmouthshire | Sir Fynwy | Usk STW | 1700 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338020 | 201015 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BU | NP151BU | np15 1bu | np151bu | Monmouthshire | Sir Fynwy | Usk STW | 1745 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337856 | 200987 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BW | NP151BW | np15 1bw | np151bw | Monmouthshire | Sir Fynwy | Usk STW | 1706 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337866 | 200948 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BX | NP151BX | np15 1bx | np151bx | Monmouthshire | Sir Fynwy | Usk STW | 1550 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337975 | 200829 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BY | NP151BY | np15 1by | np151by | Monmouthshire | Sir Fynwy | Usk STW | 1679 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337875 | 200922 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1BZ | NP151BZ | np15 1bz | np151bz | Monmouthshire | Sir Fynwy | Usk STW | 1679 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337971 | 200970 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DA | NP151DA | np15 1da | np151da | Monmouthshire | Sir Fynwy | Llansoy STW | 1462 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 343838 | 203508 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DB | NP151DB | np15 1db | np151db | Monmouthshire | Sir Fynwy | Gwernesney STW | 1227 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 341885 | 202492 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DD | NP151DD | np15 1dd | np151dd | Monmouthshire | Sir Fynwy | Gwernesney STW | 546 | 984 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.34 | 9.78 | 10.81 | 340469 | 202354 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DE | NP151DE | np15 1de | np151de | Monmouthshire | Sir Fynwy | Llansoy STW | 1092 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 343652 | 203126 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DF | NP151DF | np15 1df | np151df | Monmouthshire | Sir Fynwy | Llansoy STW | 792 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 344378 | 202605 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DG | NP151DG | np15 1dg | np151dg | Monmouthshire | Sir Fynwy | Gwernesney STW | 997 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 340564 | 202888 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DH | NP151DH | np15 1dh | np151dh | Monmouthshire | Sir Fynwy | Llansoy STW | 1778 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 342557 | 203301 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DJ | NP151DJ | np15 1dj | np151dj | Monmouthshire | Sir Fynwy | Llansoy STW | 2293 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 343699 | 204336 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DL | NP151DL | np15 1dl | np151dl | Monmouthshire | Sir Fynwy | Gwernesney STW | 2086 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 341435 | 203906 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DN | NP151DN | np15 1dn | np151dn | Monmouthshire | Sir Fynwy | Raglan STW | 2404 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 342378 | 204857 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DP | NP151DP | np15 1dp | np151dp | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 2490 | 981 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.28 | 9.75 | 10.78 | 340936 | 204755 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DQ | NP151DQ | np15 1dq | np151dq | Monmouthshire | Sir Fynwy | Usk STW | 1534 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337517 | 200449 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DR | NP151DR | np15 1dr | np151dr | Monmouthshire | Sir Fynwy | Gwernesney STW | 2555 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 339984 | 204340 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DS | NP151DS | np15 1ds | np151ds | Monmouthshire | Sir Fynwy | Raglan STW | 2245 | 914 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.04 | 9.09 | 10.04 | 342958 | 205329 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DT | NP151DT | np15 1dt | np151dt | Monmouthshire | Sir Fynwy | Llansoy STW | 1997 | 992 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.49 | 9.86 | 10.9 | 345785 | 202377 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DU | NP151DU | np15 1du | np151du | Monmouthshire | Sir Fynwy | Llanishen STW | 1720 | 992 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.49 | 9.86 | 10.9 | 346450 | 201859 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DW | NP151DW | np15 1dw | np151dw | Monmouthshire | Sir Fynwy | Raglan STW | 2164 | 914 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.04 | 9.09 | 10.04 | 342559 | 205186 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DX | NP151DX | np15 1dx | np151dx | Monmouthshire | Sir Fynwy | Llansoy STW | 504 | 972 | 900to1200 | 1.95 | 1.42 | 1.04 | 18.12 | 9.66 | 10.68 | 344200 | 202373 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DY | NP151DY | np15 1dy | np151dy | Monmouthshire | Sir Fynwy | Gwernesney STW | 753 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 340592 | 202643 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1DZ | NP151DZ | np15 1dz | np151dz | Monmouthshire | Sir Fynwy | Gwernesney STW | 2056 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 341334 | 203905 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EB | NP151EB | np15 1eb | np151eb | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 2796 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 340126 | 204712 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1ED | NP151ED | np15 1ed | np151ed | Monmouthshire | Sir Fynwy | Usk STW | 1724 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337636 | 200820 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EE | NP151EE | np15 1ee | np151ee | Monmouthshire | Sir Fynwy | Raglan STW | 2187 | 914 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.04 | 9.09 | 10.04 | 342576 | 205169 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EF | NP151EF | np15 1ef | np151ef | Monmouthshire | Sir Fynwy | Llansoy STW | 683 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 344306 | 202523 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EG | NP151EG | np15 1eg | np151eg | Monmouthshire | Sir Fynwy | Usk STW | 1701 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337672 | 200818 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EH | NP151EH | np15 1eh | np151eh | Monmouthshire | Sir Fynwy | Llansoy STW | 2069 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 344539 | 200109 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EJ | NP151EJ | np15 1ej | np151ej | Monmouthshire | Sir Fynwy | Llansoy STW | 1044 | 976 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.19 | 9.7 | 10.72 | 342776 | 202136 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EL | NP151EL | np15 1el | np151el | Monmouthshire | Sir Fynwy | Llangybi STW | 1445 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337228 | 196815 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EN | NP151EN | np15 1en | np151en | Monmouthshire | Sir Fynwy | Usk STW | 1184 | 1048 | 900to1200 | 2.1 | 1.53 | 1.13 | 19.53 | 10.42 | 11.51 | 339280 | 200469 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EP | NP151EP | np15 1ep | np151ep | Monmouthshire | Sir Fynwy | Llansoy STW | 1116 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 342871 | 201454 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EQ | NP151EQ | np15 1eq | np151eq | Monmouthshire | Sir Fynwy | Llanvair STW | 1324 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 336159 | 206130 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1ER | NP151ER | np15 1er | np151er | Monmouthshire | Sir Fynwy | Gwernesney STW | 282 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 341061 | 201814 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1ES | NP151ES | np15 1es | np151es | Monmouthshire | Sir Fynwy | Gwernesney STW | 291 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 341059 | 201788 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1ET | NP151ET | np15 1et | np151et | Monmouthshire | Sir Fynwy | Gwernesney STW | 1797 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 342148 | 200732 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EU | NP151EU | np15 1eu | np151eu | Monmouthshire | Sir Fynwy | Llansoy STW | 1809 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 342570 | 200736 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EW | NP151EW | np15 1ew | np151ew | Monmouthshire | Sir Fynwy | Usk STW | 1483 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338424 | 200909 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EX | NP151EX | np15 1ex | np151ex | Monmouthshire | Sir Fynwy | Llansoy STW | 718 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 343983 | 201349 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EY | NP151EY | np15 1ey | np151ey | Monmouthshire | Sir Fynwy | Gwernesney STW | 1148 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 340077 | 201029 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1EZ | NP151EZ | np15 1ez | np151ez | Monmouthshire | Sir Fynwy | Gwernesney STW | 1381 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 341102 | 200573 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1FA | NP151FA | np15 1fa | np151fa | Monmouthshire | Sir Fynwy | Gwernesney STW | 1841 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 339565 | 203284 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1FB | NP151FB | np15 1fb | np151fb | Monmouthshire | Sir Fynwy | Usk STW | 1655 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337834 | 200871 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1GA | NP151GA | np15 1ga | np151ga | Monmouthshire | Sir Fynwy | Little Mill STW | 2982 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 336686 | 201885 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1GY | NP151GY | np15 1gy | np151gy | Monmouthshire | Sir Fynwy | Goytre STW | 1890 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 335966 | 204271 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1GZ | NP151GZ | np15 1gz | np151gz | Monmouthshire | Sir Fynwy | Usk STW | 1671 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338074 | 201006 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HA | NP151HA | np15 1ha | np151ha | Monmouthshire | Sir Fynwy | Llansoy STW | 1781 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 342667 | 200687 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HB | NP151HB | np15 1hb | np151hb | Monmouthshire | Sir Fynwy | Llansoy STW | 2095 | 1039 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.37 | 10.33 | 11.42 | 343605 | 199963 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HD | NP151HD | np15 1hd | np151hd | Monmouthshire | Sir Fynwy | Usk STW | 4173 | 1140 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.25 | 11.33 | 12.53 | 342600 | 198023 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HE | NP151HE | np15 1he | np151he | Monmouthshire | Sir Fynwy | Gwernesney STW | 731 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 341525 | 201825 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HF | NP151HF | np15 1hf | np151hf | Monmouthshire | Sir Fynwy | Gwernesney STW | 469 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 341143 | 201600 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HG | NP151HG | np15 1hg | np151hg | Monmouthshire | Sir Fynwy | Llansoy STW | 2446 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 342567 | 199945 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HH | NP151HH | np15 1hh | np151hh | Monmouthshire | Sir Fynwy | Llansoy STW | 2885 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 342732 | 199374 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HJ | NP151HJ | np15 1hj | np151hj | Monmouthshire | Sir Fynwy | Devauden STW | 3276 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 344010 | 198548 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HL | NP151HL | np15 1hl | np151hl | Monmouthshire | Sir Fynwy | Llansoy STW | 614 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 344209 | 202518 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HN | NP151HN | np15 1hn | np151hn | Monmouthshire | Sir Fynwy | Usk STW | 1531 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338354 | 200944 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HP | NP151HP | np15 1hp | np151hp | Monmouthshire | Sir Fynwy | Llansoy STW | 2428 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 342654 | 199916 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HQ | NP151HQ | np15 1hq | np151hq | Monmouthshire | Sir Fynwy | Llansoy STW | 2313 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 342714 | 200014 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HR | NP151HR | np15 1hr | np151hr | Monmouthshire | Sir Fynwy | Goytre STW | 1721 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 336175 | 205386 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HS | NP151HS | np15 1hs | np151hs | Monmouthshire | Sir Fynwy | Gwernesney STW | 3414 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 338063 | 203958 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HT | NP151HT | np15 1ht | np151ht | Monmouthshire | Sir Fynwy | Goytre STW | 2325 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 336561 | 204423 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HU | NP151HU | np15 1hu | np151hu | Monmouthshire | Sir Fynwy | Usk STW | 3085 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 337695 | 202371 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HW | NP151HW | np15 1hw | np151hw | Monmouthshire | Sir Fynwy | Llansoy STW | 2495 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 342518 | 199917 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HX | NP151HX | np15 1hx | np151hx | Monmouthshire | Sir Fynwy | Usk STW | 2878 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 337248 | 201944 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HY | NP151HY | np15 1hy | np151hy | Monmouthshire | Sir Fynwy | Little Mill STW | 3012 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 336696 | 203021 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1HZ | NP151HZ | np15 1hz | np151hz | Monmouthshire | Sir Fynwy | Goytre STW | 3409 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 337117 | 203277 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JA | NP151JA | np15 1ja | np151ja | Monmouthshire | Sir Fynwy | Little Mill STW | 3119 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 336769 | 203179 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JB | NP151JB | np15 1jb | np151jb | Monmouthshire | Sir Fynwy | Little Mill STW | 3162 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 336804 | 203215 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JD | NP151JD | np15 1jd | np151jd | Monmouthshire | Sir Fynwy | Goytre STW | 780 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 334845 | 204730 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JE | NP151JE | np15 1je | np151je | Monmouthshire | Sir Fynwy | Goytre STW | 3359 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 337110 | 203350 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JF | NP151JF | np15 1jf | np151jf | Monmouthshire | Sir Fynwy | Little Mill STW | 3067 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 336763 | 202969 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JG | NP151JG | np15 1jg | np151jg | Monmouthshire | Sir Fynwy | Little Mill STW | 3073 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 336709 | 203227 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JH | NP151JH | np15 1jh | np151jh | Monmouthshire | Sir Fynwy | Gwernesney STW | 3466 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 338208 | 204219 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JJ | NP151JJ | np15 1jj | np151jj | Monmouthshire | Sir Fynwy | Llanvair STW | 972 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 335922 | 206464 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JL | NP151JL | np15 1jl | np151jl | Monmouthshire | Sir Fynwy | Llanvair STW | 414 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 335408 | 206837 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JN | NP151JN | np15 1jn | np151jn | Monmouthshire | Sir Fynwy | Llanvair STW | 1359 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 336101 | 205974 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JP | NP151JP | np15 1jp | np151jp | Monmouthshire | Sir Fynwy | Llanvair STW | 326 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 335312 | 206865 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JQ | NP151JQ | np15 1jq | np151jq | Monmouthshire | Sir Fynwy | Little Mill STW | 3161 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 336790 | 203263 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JR | NP151JR | np15 1jr | np151jr | Monmouthshire | Sir Fynwy | Llanvair STW | 1171 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 335958 | 207443 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JS | NP151JS | np15 1js | np151js | Monmouthshire | Sir Fynwy | Llanvair STW | 1515 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 336459 | 206364 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JT | NP151JT | np15 1jt | np151jt | Monmouthshire | Sir Fynwy | Llanvair STW | 861 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 335633 | 207353 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JU | NP151JU | np15 1ju | np151ju | Monmouthshire | Sir Fynwy | Goytre STW | 717 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 334868 | 204819 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JW | NP151JW | np15 1jw | np151jw | Monmouthshire | Sir Fynwy | Llanvair STW | 1158 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 336035 | 206251 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JX | NP151JX | np15 1jx | np151jx | Monmouthshire | Sir Fynwy | Goytre STW | 2425 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 336637 | 204350 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JY | NP151JY | np15 1jy | np151jy | Monmouthshire | Sir Fynwy | Llanvair STW | 976 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 335584 | 205988 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1JZ | NP151JZ | np15 1jz | np151jz | Monmouthshire | Sir Fynwy | Goytre STW | 456 | 1078 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.09 | 10.72 | 11.84 | 334837 | 205653 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LA | NP151LA | np15 1la | np151la | Monmouthshire | Sir Fynwy | Llanvair STW | 3463 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 337974 | 204999 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LB | NP151LB | np15 1lb | np151lb | Monmouthshire | Sir Fynwy | Llanvair STW | 2758 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 337592 | 205830 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LD | NP151LD | np15 1ld | np151ld | Monmouthshire | Sir Fynwy | Goytre STW | 1292 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 335501 | 204648 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LE | NP151LE | np15 1le | np151le | Monmouthshire | Sir Fynwy | Usk STW | 1945 | 1044 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.46 | 10.38 | 11.47 | 339639 | 197758 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LG | NP151LG | np15 1lg | np151lg | Monmouthshire | Sir Fynwy | Llangybi STW | 935 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 339107 | 196780 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LH | NP151LH | np15 1lh | np151lh | Monmouthshire | Sir Fynwy | Usk STW | 270 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 338443 | 199578 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LJ | NP151LJ | np15 1lj | np151lj | Monmouthshire | Sir Fynwy | Usk STW | 995 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 339310 | 198679 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LL | NP151LL | np15 1ll | np151ll | Monmouthshire | Sir Fynwy | Usk STW | 1795 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 340407 | 198962 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LN | NP151LN | np15 1ln | np151ln | Monmouthshire | Sir Fynwy | Llangybi STW | 2458 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 340688 | 197163 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LP | NP151LP | np15 1lp | np151lp | Monmouthshire | Sir Fynwy | Usk STW | 1673 | 1044 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.46 | 10.38 | 11.47 | 339803 | 198210 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LQ | NP151LQ | np15 1lq | np151lq | Monmouthshire | Sir Fynwy | Llangybi STW | 1057 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 339104 | 196940 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LR | NP151LR | np15 1lr | np151lr | Monmouthshire | Sir Fynwy | Llangybi STW | 1432 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 339442 | 195033 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LS | NP151LS | np15 1ls | np151ls | Monmouthshire | Sir Fynwy | Usk STW | 2186 | 1044 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.46 | 10.38 | 11.47 | 339989 | 197699 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LT | NP151LT | np15 1lt | np151lt | Monmouthshire | Sir Fynwy | Gwernesney STW | 2677 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 341650 | 199383 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LU | NP151LU | np15 1lu | np151lu | Monmouthshire | Sir Fynwy | Llangybi STW | 2400 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 340876 | 196058 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LW | NP151LW | np15 1lw | np151lw | Monmouthshire | Sir Fynwy | Llangybi STW | 1800 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 340026 | 197006 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LY | NP151LY | np15 1ly | np151ly | Monmouthshire | Sir Fynwy | Tredunnock STW | 372 | 1044 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.46 | 10.38 | 11.47 | 338067 | 194749 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1LZ | NP151LZ | np15 1lz | np151lz | Monmouthshire | Sir Fynwy | Tredunnock STW | 348 | 1044 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.46 | 10.38 | 11.47 | 338022 | 194758 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NB | NP151NB | np15 1nb | np151nb | Monmouthshire | Sir Fynwy | Usk STW | 505 | 1048 | 900to1200 | 2.1 | 1.53 | 1.13 | 19.53 | 10.42 | 11.51 | 338973 | 199860 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1ND | NP151ND | np15 1nd | np151nd | Monmouthshire | Sir Fynwy | Llangybi STW | 2747 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 341032 | 195083 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NE | NP151NE | np15 1ne | np151ne | Monmouthshire | Sir Fynwy | Usk STW | 2263 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 340942 | 199444 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NF | NP151NF | np15 1nf | np151nf | Monmouthshire | Sir Fynwy | Usk STW | 2442 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 341104 | 199158 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NG | NP151NG | np15 1ng | np151ng | Monmouthshire | Sir Fynwy | Llangybi STW | 3284 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 341507 | 197354 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NH | NP151NH | np15 1nh | np151nh | Monmouthshire | Sir Fynwy | Usk STW | 2338 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 340974 | 199001 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NJ | NP151NJ | np15 1nj | np151nj | Monmouthshire | Sir Fynwy | Llangybi STW | 1919 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337131 | 197457 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NL | NP151NL | np15 1nl | np151nl | Monmouthshire | Sir Fynwy | Llangybi STW | 1551 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337062 | 196723 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NN | NP151NN | np15 1nn | np151nn | Monmouthshire | Sir Fynwy | Usk STW | 1637 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 337467 | 198351 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NP | NP151NP | np15 1np | np151np | Monmouthshire | Sir Fynwy | Llangybi STW | 1281 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337314 | 196625 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NQ | NP151NQ | np15 1nq | np151nq | Monmouthshire | Sir Fynwy | Llangybi STW | 3541 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 341773 | 197382 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NR | NP151NR | np15 1nr | np151nr | Monmouthshire | Sir Fynwy | Llangybi STW | 1385 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337228 | 196687 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NS | NP151NS | np15 1ns | np151ns | Monmouthshire | Sir Fynwy | Tredunnock STW | 595 | 1132 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.1 | 11.25 | 12.44 | 337308 | 194837 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NT | NP151NT | np15 1nt | np151nt | Monmouthshire | Sir Fynwy | Llangybi STW | 1427 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337129 | 196558 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NU | NP151NU | np15 1nu | np151nu | Monmouthshire | Sir Fynwy | Llangybi STW | 1395 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337168 | 196570 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NW | NP151NW | np15 1nw | np151nw | Monmouthshire | Sir Fynwy | Usk STW | 1646 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 337470 | 198334 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NX | NP151NX | np15 1nx | np151nx | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 1583 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 335542 | 195705 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NY | NP151NY | np15 1ny | np151ny | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 2197 | 1222 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.78 | 12.15 | 13.43 | 335074 | 197266 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1NZ | NP151NZ | np15 1nz | np151nz | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 1678 | 1222 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.78 | 12.15 | 13.43 | 334985 | 196708 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PA | NP151PA | np15 1pa | np151pa | Monmouthshire | Sir Fynwy | Llangybi STW | 1405 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 337131 | 196490 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PB | NP151PB | np15 1pb | np151pb | Monmouthshire | Sir Fynwy | Llangybi STW | 2116 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 336362 | 196075 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PD | NP151PD | np15 1pd | np151pd | Monmouthshire | Sir Fynwy | Tredunnock STW | 1866 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 336496 | 195834 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PE | NP151PE | np15 1pe | np151pe | Monmouthshire | Sir Fynwy | Tredunnock STW | 884 | 1132 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.1 | 11.25 | 12.44 | 337189 | 195138 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PF | NP151PF | np15 1pf | np151pf | Monmouthshire | Sir Fynwy | Tredunnock STW | 1260 | 1132 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.1 | 11.25 | 12.44 | 336578 | 194821 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PG | NP151PG | np15 1pg | np151pg | Monmouthshire | Sir Fynwy | Tredunnock STW | 1386 | 1132 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.1 | 11.25 | 12.44 | 336777 | 195435 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PH | NP151PH | np15 1ph | np151ph | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 1431 | 1174 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.88 | 11.67 | 12.9 | 335387 | 195702 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PJ | NP151PJ | np15 1pj | np151pj | Monmouthshire | Sir Fynwy | Llangybi STW | 1355 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337256 | 196677 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PL | NP151PL | np15 1pl | np151pl | Monmouthshire | Sir Fynwy | Usk STW | 1323 | 1074 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.02 | 10.68 | 11.8 | 337514 | 198824 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PN | NP151PN | np15 1pn | np151pn | Monmouthshire | Sir Fynwy | Llangybi STW | 1617 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 336977 | 196692 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PP | NP151PP | np15 1pp | np151pp | Monmouthshire | Sir Fynwy | Goytre STW | 362 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 334815 | 205373 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PQ | NP151PQ | np15 1pq | np151pq | Monmouthshire | Sir Fynwy | Llangybi STW | 1322 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337363 | 196801 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PR | NP151PR | np15 1pr | np151pr | Monmouthshire | Sir Fynwy | Usk STW | 2034 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 336757 | 200109 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PS | NP151PS | np15 1ps | np151ps | Monmouthshire | Sir Fynwy | Usk STW | 3144 | 1145 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.34 | 11.38 | 12.58 | 335537 | 199474 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PT | NP151PT | np15 1pt | np151pt | Monmouthshire | Sir Fynwy | Little Mill STW | 2704 | 1168 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.77 | 11.61 | 12.83 | 334641 | 199848 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PU | NP151PU | np15 1pu | np151pu | Monmouthshire | Sir Fynwy | Little Mill STW | 2947 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 336692 | 202251 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PW | NP151PW | np15 1pw | np151pw | Monmouthshire | Sir Fynwy | Little Mill STW | 2280 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 336027 | 202308 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PX | NP151PX | np15 1px | np151px | Monmouthshire | Sir Fynwy | Little Mill STW | 865 | 1135 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.15 | 11.28 | 12.47 | 334415 | 202953 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PY | NP151PY | np15 1py | np151py | Monmouthshire | Sir Fynwy | Little Mill STW | 2744 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 336471 | 202055 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1PZ | NP151PZ | np15 1pz | np151pz | Monmouthshire | Sir Fynwy | Llangybi STW | 1318 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337236 | 196533 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QA | NP151QA | np15 1qa | np151qa | Monmouthshire | Sir Fynwy | Little Mill STW | 602 | 1135 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.15 | 11.28 | 12.47 | 334310 | 202619 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QB | NP151QB | np15 1qb | np151qb | Monmouthshire | Sir Fynwy | Little Mill STW | 264 | 1135 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.15 | 11.28 | 12.47 | 333772 | 202663 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QD | NP151QD | np15 1qd | np151qd | Monmouthshire | Sir Fynwy | Goytre STW | 1460 | 1135 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.15 | 11.28 | 12.47 | 333701 | 204155 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QE | NP151QE | np15 1qe | np151qe | Monmouthshire | Sir Fynwy | Little Mill STW | 1501 | 1117 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.82 | 11.1 | 12.27 | 335150 | 202939 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QF | NP151QF | np15 1qf | np151qf | Monmouthshire | Sir Fynwy | Llangybi STW | 1402 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337176 | 196612 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QG | NP151QG | np15 1qg | np151qg | Monmouthshire | Sir Fynwy | Little Mill STW | 789 | 1135 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.15 | 11.28 | 12.47 | 333502 | 203149 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QH | NP151QH | np15 1qh | np151qh | Monmouthshire | Sir Fynwy | Little Mill STW | 647 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 333321 | 202884 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QJ | NP151QJ | np15 1qj | np151qj | Monmouthshire | Sir Fynwy | Little Mill STW | 702 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 333259 | 202901 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QL | NP151QL | np15 1ql | np151ql | Monmouthshire | Sir Fynwy | Little Mill STW | 564 | 1135 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.15 | 11.28 | 12.47 | 334302 | 202517 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QN | NP151QN | np15 1qn | np151qn | Monmouthshire | Sir Fynwy | Usk STW | 1866 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338300 | 201275 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QP | NP151QP | np15 1qp | np151qp | Monmouthshire | Sir Fynwy | Little Mill STW | 1362 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 333433 | 203724 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QQ | NP151QQ | np15 1qq | np151qq | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 1805 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 335804 | 195344 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QR | NP151QR | np15 1qr | np151qr | Monmouthshire | Sir Fynwy | Little Mill STW | 627 | 1135 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.15 | 11.28 | 12.47 | 334351 | 202578 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QS | NP151QS | np15 1qs | np151qs | Monmouthshire | Sir Fynwy | Little Mill STW | 937 | 1135 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.15 | 11.28 | 12.47 | 334161 | 203242 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QT | NP151QT | np15 1qt | np151qt | Monmouthshire | Sir Fynwy | Little Mill STW | 1545 | 1135 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.15 | 11.28 | 12.47 | 333674 | 203943 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QU | NP151QU | np15 1qu | np151qu | Monmouthshire | Sir Fynwy | Llangybi STW | 1488 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337139 | 196740 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QW | NP151QW | np15 1qw | np151qw | Monmouthshire | Sir Fynwy | Usk STW | 1747 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337955 | 201038 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QX | NP151QX | np15 1qx | np151qx | Monmouthshire | Sir Fynwy | Gwernesney STW | 2016 | 1045 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.48 | 10.39 | 11.48 | 338794 | 201724 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QY | NP151QY | np15 1qy | np151qy | Monmouthshire | Sir Fynwy | Usk STW | 2068 | 1045 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.48 | 10.39 | 11.48 | 338635 | 201516 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1QZ | NP151QZ | np15 1qz | np151qz | Monmouthshire | Sir Fynwy | Usk STW | 1945 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338387 | 201371 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RA | NP151RA | np15 1ra | np151ra | Monmouthshire | Sir Fynwy | Gwernesney STW | 1093 | 984 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.34 | 9.78 | 10.81 | 339718 | 202069 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RB | NP151RB | np15 1rb | np151rb | Monmouthshire | Sir Fynwy | Gwernesney STW | 2293 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 339223 | 203584 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RD | NP151RD | np15 1rd | np151rd | Monmouthshire | Sir Fynwy | Gwernesney STW | 3478 | 1025 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.1 | 10.19 | 11.26 | 338755 | 204732 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RE | NP151RE | np15 1re | np151re | Monmouthshire | Sir Fynwy | Gwernesney STW | 2858 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 338539 | 203667 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RF | NP151RF | np15 1rf | np151rf | Monmouthshire | Sir Fynwy | Llangybi STW | 1238 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337348 | 196596 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RG | NP151RG | np15 1rg | np151rg | Monmouthshire | Sir Fynwy | Gwernesney STW | 2884 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 338948 | 204130 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RH | NP151RH | np15 1rh | np151rh | Monmouthshire | Sir Fynwy | Gwernesney STW | 3387 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 338607 | 204500 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RJ | NP151RJ | np15 1rj | np151rj | Monmouthshire | Sir Fynwy | Gwernesney STW | 1958 | 1048 | 900to1200 | 2.1 | 1.53 | 1.13 | 19.53 | 10.42 | 11.51 | 339086 | 202865 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RL | NP151RL | np15 1rl | np151rl | Monmouthshire | Sir Fynwy | Gwernesney STW | 2191 | 1048 | 900to1200 | 2.1 | 1.53 | 1.13 | 19.53 | 10.42 | 11.51 | 339183 | 203397 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RP | NP151RP | np15 1rp | np151rp | Monmouthshire | Sir Fynwy | Gwernesney STW | 2993 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 338923 | 204250 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RQ | NP151RQ | np15 1rq | np151rq | Monmouthshire | Sir Fynwy | Gwernesney STW | 2738 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 338956 | 203942 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RR | NP151RR | np15 1rr | np151rr | Monmouthshire | Sir Fynwy | Usk STW | 1959 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 338650 | 201407 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RS | NP151RS | np15 1rs | np151rs | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 3190 | 1025 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.1 | 10.19 | 11.26 | 339188 | 204903 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RT | NP151RT | np15 1rt | np151rt | Monmouthshire | Sir Fynwy | Gwernesney STW | 3131 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 338823 | 204347 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RU | NP151RU | np15 1ru | np151ru | Monmouthshire | Sir Fynwy | Usk STW | 2072 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 337460 | 201123 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RW | NP151RW | np15 1rw | np151rw | Monmouthshire | Sir Fynwy | Usk STW | 1759 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337716 | 200919 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RX | NP151RX | np15 1rx | np151rx | Monmouthshire | Sir Fynwy | Usk STW | 1875 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337524 | 200924 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RY | NP151RY | np15 1ry | np151ry | Monmouthshire | Sir Fynwy | Usk STW | 1846 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337641 | 200974 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1RZ | NP151RZ | np15 1rz | np151rz | Monmouthshire | Sir Fynwy | Usk STW | 1963 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337561 | 201061 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SA | NP151SA | np15 1sa | np151sa | Monmouthshire | Sir Fynwy | Usk STW | 1981 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337577 | 201094 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SB | NP151SB | np15 1sb | np151sb | Monmouthshire | Sir Fynwy | Usk STW | 2290 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 337425 | 201363 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SD | NP151SD | np15 1sd | np151sd | Monmouthshire | Sir Fynwy | Usk STW | 1883 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337753 | 201087 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SE | NP151SE | np15 1se | np151se | Monmouthshire | Sir Fynwy | Usk STW | 1834 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337937 | 201125 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SF | NP151SF | np15 1sf | np151sf | Monmouthshire | Sir Fynwy | Usk STW | 1884 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338140 | 201253 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SG | NP151SG | np15 1sg | np151sg | Monmouthshire | Sir Fynwy | Usk STW | 2085 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337921 | 201390 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SH | NP151SH | np15 1sh | np151sh | Monmouthshire | Sir Fynwy | Usk STW | 2010 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338014 | 201345 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SJ | NP151SJ | np15 1sj | np151sj | Monmouthshire | Sir Fynwy | Usk STW | 1959 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337962 | 201271 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SL | NP151SL | np15 1sl | np151sl | Monmouthshire | Sir Fynwy | Usk STW | 1913 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338057 | 201257 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SN | NP151SN | np15 1sn | np151sn | Monmouthshire | Sir Fynwy | Usk STW | 2156 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338004 | 201496 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SP | NP151SP | np15 1sp | np151sp | Monmouthshire | Sir Fynwy | Usk STW | 2088 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338089 | 201451 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SQ | NP151SQ | np15 1sq | np151sq | Monmouthshire | Sir Fynwy | Usk STW | 2003 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338175 | 201387 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SR | NP151SR | np15 1sr | np151sr | Monmouthshire | Sir Fynwy | Usk STW | 1946 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338240 | 201344 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SS | NP151SS | np15 1ss | np151ss | Monmouthshire | Sir Fynwy | Usk STW | 1863 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 337268 | 200664 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1ST | NP151ST | np15 1st | np151st | Monmouthshire | Sir Fynwy | Usk STW | 1967 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338162 | 201346 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SU | NP151SU | np15 1su | np151su | Monmouthshire | Sir Fynwy | Usk STW | 1664 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 337313 | 200397 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SW | NP151SW | np15 1sw | np151sw | Monmouthshire | Sir Fynwy | Usk STW | 1800 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 337459 | 200771 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SX | NP151SX | np15 1sx | np151sx | Monmouthshire | Sir Fynwy | Usk STW | 1155 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337644 | 199959 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SY | NP151SY | np15 1sy | np151sy | Monmouthshire | Sir Fynwy | Usk STW | 2170 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 337192 | 201027 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1SZ | NP151SZ | np15 1sz | np151sz | Monmouthshire | Sir Fynwy | Usk STW | 2171 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 337303 | 201126 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TA | NP151TA | np15 1ta | np151ta | Monmouthshire | Sir Fynwy | Usk STW | 1111 | 1074 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.02 | 10.68 | 11.8 | 337583 | 199273 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TB | NP151TB | np15 1tb | np151tb | Monmouthshire | Sir Fynwy | Usk STW | 1457 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 337320 | 198929 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TD | NP151TD | np15 1td | np151td | Monmouthshire | Sir Fynwy | Usk STW | 1163 | 1074 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.02 | 10.68 | 11.8 | 337541 | 199216 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TE | NP151TE | np15 1te | np151te | Monmouthshire | Sir Fynwy | Usk STW | 1191 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337589 | 199926 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TF | NP151TF | np15 1tf | np151tf | Monmouthshire | Sir Fynwy | Usk STW | 1224 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337584 | 199992 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TG | NP151TG | np15 1tg | np151tg | Monmouthshire | Sir Fynwy | Usk STW | 999 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337684 | 199524 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TH | NP151TH | np15 1th | np151th | Monmouthshire | Sir Fynwy | Usk STW | 1983 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 336784 | 198872 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TJ | NP151TJ | np15 1tj | np151tj | Monmouthshire | Sir Fynwy | Usk STW | 1880 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 337346 | 200773 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TL | NP151TL | np15 1tl | np151tl | Monmouthshire | Sir Fynwy | Usk STW | 773 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337937 | 199663 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TN | NP151TN | np15 1tn | np151tn | Monmouthshire | Sir Fynwy | Usk STW | 2102 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338192 | 201493 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TP | NP151TP | np15 1tp | np151tp | Monmouthshire | Sir Fynwy | Usk STW | 1919 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 336811 | 199018 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TQ | NP151TQ | np15 1tq | np151tq | Monmouthshire | Sir Fynwy | Usk STW | 1097 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337623 | 199741 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TR | NP151TR | np15 1tr | np151tr | Monmouthshire | Sir Fynwy | Usk STW | 2171 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 338190 | 201563 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TS | NP151TS | np15 1ts | np151ts | Monmouthshire | Sir Fynwy | Usk STW | 2091 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 338153 | 201472 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TT | NP151TT | np15 1tt | np151tt | Monmouthshire | Sir Fynwy | Llangybi STW | 1492 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337073 | 196594 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TU | NP151TU | np15 1tu | np151tu | Monmouthshire | Sir Fynwy | Llangybi STW | 1553 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 336984 | 196515 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TW | NP151TW | np15 1tw | np151tw | Monmouthshire | Sir Fynwy | Llangybi STW | 1619 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 336959 | 196650 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TX | NP151TX | np15 1tx | np151tx | Monmouthshire | Sir Fynwy | Llangybi STW | 1390 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 337278 | 196793 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TY | NP151TY | np15 1ty | np151ty | Monmouthshire | Sir Fynwy | Llangybi STW | 1547 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 336980 | 196478 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1TZ | NP151TZ | np15 1tz | np151tz | Monmouthshire | Sir Fynwy | Usk STW | 2131 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 338295 | 201544 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1UA | NP151UA | np15 1ua | np151ua | Monmouthshire | Sir Fynwy | Usk STW | 1528 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337693 | 200615 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1XD | NP151XD | np15 1xd | np151xd | Monmouthshire | Sir Fynwy | Usk STW | 1759 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337577 | 200819 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1XJ | NP151XJ | np15 1xj | np151xj | Monmouthshire | Sir Fynwy | Little Mill STW | 2858 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 336550 | 201830 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1XL | NP151XL | np15 1xl | np151xl | Monmouthshire | Sir Fynwy | Little Mill STW | 1411 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 334876 | 201551 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1XP | NP151XP | np15 1xp | np151xp | Monmouthshire | Sir Fynwy | Usk STW | 1300 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 337863 | 200460 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1XQ | NP151XQ | np15 1xq | np151xq | Monmouthshire | Sir Fynwy | Usk STW | 1784 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337512 | 200797 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 1YS | NP151YS | np15 1ys | np151ys | Monmouthshire | Sir Fynwy | Usk STW | 1784 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337512 | 200797 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AA | NP152AA | np15 2aa | np152aa | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 1380 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 340268 | 207989 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AB | NP152AB | np15 2ab | np152ab | Monmouthshire | Sir Fynwy | Great Oak STW | 1476 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 339105 | 208898 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AD | NP152AD | np15 2ad | np152ad | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 428 | 957 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.84 | 9.51 | 10.51 | 341000 | 207352 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AE | NP152AE | np15 2ae | np152ae | Monmouthshire | Sir Fynwy | Great Oak STW | 1304 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 339089 | 209093 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AF | NP152AF | np15 2af | np152af | Monmouthshire | Sir Fynwy | Great Oak STW | 1364 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 338959 | 208945 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AG | NP152AG | np15 2ag | np152ag | Monmouthshire | Sir Fynwy | Great Oak STW | 595 | 1008 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.79 | 10.02 | 11.07 | 338566 | 209610 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AH | NP152AH | np15 2ah | np152ah | Monmouthshire | Sir Fynwy | Great Oak STW | 320 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 338495 | 209880 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AJ | NP152AJ | np15 2aj | np152aj | Monmouthshire | Sir Fynwy | Great Oak STW | 239 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 338472 | 209961 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AL | NP152AL | np15 2al | np152al | Monmouthshire | Sir Fynwy | Great Oak STW | 211 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 338496 | 210018 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AN | NP152AN | np15 2an | np152an | Monmouthshire | Sir Fynwy | Great Oak STW | 275 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 338491 | 209930 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AP | NP152AP | np15 2ap | np152ap | Monmouthshire | Sir Fynwy | Llanarth STW | 908 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 337325 | 209693 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AQ | NP152AQ | np15 2aq | np152aq | Monmouthshire | Sir Fynwy | Great Oak STW | 453 | 1008 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.79 | 10.02 | 11.07 | 338604 | 209792 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AR | NP152AR | np15 2ar | np152ar | Monmouthshire | Sir Fynwy | Llanarth STW | 734 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 337189 | 210047 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AS | NP152AS | np15 2as | np152as | Monmouthshire | Sir Fynwy | Llanarth STW | 479 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 337674 | 210943 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AT | NP152AT | np15 2at | np152at | Monmouthshire | Sir Fynwy | Llanarth STW | 528 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 337634 | 210983 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AU | NP152AU | np15 2au | np152au | Monmouthshire | Sir Fynwy | Llanarth STW | 582 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 337514 | 210993 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AW | NP152AW | np15 2aw | np152aw | Monmouthshire | Sir Fynwy | Llanarth STW | 882 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 337403 | 209681 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AX | NP152AX | np15 2ax | np152ax | Monmouthshire | Sir Fynwy | Llanarth STW | 617 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 337580 | 211059 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AY | NP152AY | np15 2ay | np152ay | Monmouthshire | Sir Fynwy | Llanarth STW | 717 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 337520 | 211144 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2AZ | NP152AZ | np15 2az | np152az | Monmouthshire | Sir Fynwy | Llanarth STW | 544 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 337269 | 210299 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BA | NP152BA | np15 2ba | np152ba | Monmouthshire | Sir Fynwy | Llanarth STW | 794 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 337140 | 210011 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BB | NP152BB | np15 2bb | np152bb | Monmouthshire | Sir Fynwy | Llanarth STW | 824 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 337209 | 209886 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BD | NP152BD | np15 2bd | np152bd | Monmouthshire | Sir Fynwy | Llanarth STW | 848 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 337238 | 209828 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BE | NP152BE | np15 2be | np152be | Monmouthshire | Sir Fynwy | Llanarth STW | 930 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 337345 | 209657 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BG | NP152BG | np15 2bg | np152bg | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 2103 | 982 | 900to1200 | 1.97 | 1.44 | 1.05 | 18.3 | 9.76 | 10.79 | 339981 | 208751 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BH | NP152BH | np15 2bh | np152bh | Monmouthshire | Sir Fynwy | Great Oak STW | 1464 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 338820 | 208777 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BJ | NP152BJ | np15 2bj | np152bj | Monmouthshire | Sir Fynwy | Great Oak STW | 242 | 1008 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.79 | 10.02 | 11.07 | 338502 | 209980 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BL | NP152BL | np15 2bl | np152bl | Monmouthshire | Sir Fynwy | Great Oak STW | 732 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 338629 | 209488 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BN | NP152BN | np15 2bn | np152bn | Monmouthshire | Sir Fynwy | Great Oak STW | 613 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 337934 | 209701 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BP | NP152BP | np15 2bp | np152bp | Monmouthshire | Sir Fynwy | Llanarth STW | 1237 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 337312 | 209334 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BQ | NP152BQ | np15 2bq | np152bq | Monmouthshire | Sir Fynwy | Great Oak STW | 1135 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 338214 | 209032 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BR | NP152BR | np15 2br | np152br | Monmouthshire | Sir Fynwy | Llanarth STW | 844 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 337093 | 209991 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BS | NP152BS | np15 2bs | np152bs | Monmouthshire | Sir Fynwy | Great Oak STW | 1329 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 338533 | 208846 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BT | NP152BT | np15 2bt | np152bt | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 1173 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341572 | 208360 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BW | NP152BW | np15 2bw | np152bw | Monmouthshire | Sir Fynwy | Great Oak STW | 1710 | 962 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.93 | 9.56 | 10.57 | 339962 | 209619 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BX | NP152BX | np15 2bx | np152bx | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 1132 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 340785 | 208150 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BY | NP152BY | np15 2by | np152by | Monmouthshire | Sir Fynwy | Penrhos STW | 2033 | 951 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.73 | 9.45 | 10.45 | 341203 | 209530 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2BZ | NP152BZ | np15 2bz | np152bz | Monmouthshire | Sir Fynwy | Great Oak STW | 1802 | 962 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.93 | 9.56 | 10.57 | 340101 | 209779 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DA | NP152DA | np15 2da | np152da | Monmouthshire | Sir Fynwy | Great Oak STW | 1150 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 339227 | 209429 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DB | NP152DB | np15 2db | np152db | Monmouthshire | Sir Fynwy | Great Oak STW | 1046 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 339012 | 209359 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DD | NP152DD | np15 2dd | np152dd | Monmouthshire | Sir Fynwy | Great Oak STW | 571 | 1008 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.79 | 10.02 | 11.07 | 338733 | 209746 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DE | NP152DE | np15 2de | np152de | Monmouthshire | Sir Fynwy | Great Oak STW | 1443 | 987 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.4 | 9.81 | 10.84 | 339081 | 211398 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DF | NP152DF | np15 2df | np152df | Monmouthshire | Sir Fynwy | Penrhos STW | 1604 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 340023 | 212164 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DJ | NP152DJ | np15 2dj | np152dj | Monmouthshire | Sir Fynwy | Penrhos STW | 842 | 951 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.73 | 9.45 | 10.45 | 340842 | 212065 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DL | NP152DL | np15 2dl | np152dl | Monmouthshire | Sir Fynwy | Penrhos STW | 1155 | 950 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.71 | 9.44 | 10.44 | 340738 | 210673 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DN | NP152DN | np15 2dn | np152dn | Monmouthshire | Sir Fynwy | Great Oak STW | 500 | 987 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.4 | 9.81 | 10.84 | 338611 | 210580 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DP | NP152DP | np15 2dp | np152dp | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 557 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341228 | 207730 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DR | NP152DR | np15 2dr | np152dr | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 645 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341138 | 207789 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DS | NP152DS | np15 2ds | np152ds | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 552 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341325 | 207747 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DT | NP152DT | np15 2dt | np152dt | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 660 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341324 | 207855 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DU | NP152DU | np15 2du | np152du | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 682 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341262 | 207868 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DW | NP152DW | np15 2dw | np152dw | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 661 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341203 | 207831 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DX | NP152DX | np15 2dx | np152dx | Monmouthshire | Sir Fynwy | Raglan STW | 1535 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 342984 | 206408 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2DY | NP152DY | np15 2dy | np152dy | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 527 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341191 | 207684 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EA | NP152EA | np15 2ea | np152ea | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 650 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341086 | 207769 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EB | NP152EB | np15 2eb | np152eb | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 554 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341080 | 207652 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2ED | NP152ED | np15 2ed | np152ed | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 511 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341074 | 207593 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EE | NP152EE | np15 2ee | np152ee | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 536 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341015 | 207572 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EF | NP152EF | np15 2ef | np152ef | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 615 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 340960 | 207629 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EG | NP152EG | np15 2eg | np152eg | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 418 | 957 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.84 | 9.51 | 10.51 | 341103 | 207494 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EH | NP152EH | np15 2eh | np152eh | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 391 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341186 | 207527 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EJ | NP152EJ | np15 2ej | np152ej | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 480 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341164 | 207618 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EL | NP152EL | np15 2el | np152el | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 450 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341234 | 207618 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EN | NP152EN | np15 2en | np152en | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 356 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341359 | 207554 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EP | NP152EP | np15 2ep | np152ep | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 442 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341497 | 207631 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EQ | NP152EQ | np15 2eq | np152eq | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 466 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341099 | 207556 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2ER | NP152ER | np15 2er | np152er | Monmouthshire | Sir Fynwy | Raglan STW | 374 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 342011 | 207140 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2ES | NP152ES | np15 2es | np152es | Monmouthshire | Sir Fynwy | Raglan STW | 316 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 341879 | 207346 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2ET | NP152ET | np15 2et | np152et | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 601 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341480 | 207795 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EU | NP152EU | np15 2eu | np152eu | Monmouthshire | Sir Fynwy | Raglan STW | 1929 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 342870 | 208626 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EW | NP152EW | np15 2ew | np152ew | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 573 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341037 | 207643 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EX | NP152EX | np15 2ex | np152ex | Monmouthshire | Sir Fynwy | Raglan STW | 1724 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 342724 | 208480 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EY | NP152EY | np15 2ey | np152ey | Monmouthshire | Sir Fynwy | Raglan STW | 1378 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 342799 | 207883 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2EZ | NP152EZ | np15 2ez | np152ez | Monmouthshire | Sir Fynwy | Raglan STW | 1894 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 343512 | 206877 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2FB | NP152FB | np15 2fb | np152fb | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 457 | 957 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.84 | 9.51 | 10.51 | 340992 | 207406 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2FD | NP152FD | np15 2fd | np152fd | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 311 | 957 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.84 | 9.51 | 10.51 | 341104 | 207296 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HA | NP152HA | np15 2ha | np152ha | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 281 | 957 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.84 | 9.51 | 10.51 | 341252 | 207439 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HB | NP152HB | np15 2hb | np152hb | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 251 | 957 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.84 | 9.51 | 10.51 | 341207 | 207360 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HD | NP152HD | np15 2hd | np152hd | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 501 | 957 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.84 | 9.51 | 10.51 | 340929 | 207370 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HE | NP152HE | np15 2he | np152he | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 336 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341330 | 207529 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HF | NP152HF | np15 2hf | np152hf | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 310 | 957 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.84 | 9.51 | 10.51 | 341271 | 207482 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HG | NP152HG | np15 2hg | np152hg | Monmouthshire | Sir Fynwy | Raglan STW | 903 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341871 | 208015 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HH | NP152HH | np15 2hh | np152hh | Monmouthshire | Sir Fynwy | Raglan STW | 1652 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 342574 | 208503 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HJ | NP152HJ | np15 2hj | np152hj | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 621 | 957 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.84 | 9.51 | 10.51 | 340780 | 207226 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HL | NP152HL | np15 2hl | np152hl | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 574 | 957 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.84 | 9.51 | 10.51 | 340868 | 207415 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HN | NP152HN | np15 2hn | np152hn | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 1422 | 987 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.4 | 9.81 | 10.84 | 339998 | 206966 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HP | NP152HP | np15 2hp | np152hp | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 1180 | 976 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.19 | 9.7 | 10.72 | 340483 | 206458 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HQ | NP152HQ | np15 2hq | np152hq | Monmouthshire | Sir Fynwy | Raglan STW | 1380 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 342350 | 208324 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HR | NP152HR | np15 2hr | np152hr | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 2490 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 339399 | 205720 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HS | NP152HS | np15 2hs | np152hs | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 2603 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 339323 | 205633 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HT | NP152HT | np15 2ht | np152ht | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 1758 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 340734 | 205574 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HU | NP152HU | np15 2hu | np152hu | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 1723 | 976 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.19 | 9.7 | 10.72 | 340252 | 205916 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HW | NP152HW | np15 2hw | np152hw | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 1684 | 987 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.4 | 9.81 | 10.84 | 339780 | 206744 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HX | NP152HX | np15 2hx | np152hx | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 985 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 341148 | 206248 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HY | NP152HY | np15 2hy | np152hy | Monmouthshire | Sir Fynwy | Raglan STW | 1394 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 341742 | 205753 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2HZ | NP152HZ | np15 2hz | np152hz | Monmouthshire | Sir Fynwy | Raglan STW | 513 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 341658 | 206631 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JA | NP152JA | np15 2ja | np152ja | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 2367 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 340347 | 205081 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JB | NP152JB | np15 2jb | np152jb | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 36 | 957 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.84 | 9.51 | 10.51 | 341395 | 207164 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JG | NP152JG | np15 2jg | np152jg | Monmouthshire | Sir Fynwy | Great Oak STW | 1736 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 339378 | 208769 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JH | NP152JH | np15 2jh | np152jh | Monmouthshire | Sir Fynwy | Great Oak STW | 2301 | 1012 | 900to1200 | 2.03 | 1.48 | 1.09 | 18.86 | 10.06 | 11.12 | 338579 | 207872 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JJ | NP152JJ | np15 2jj | np152jj | Monmouthshire | Sir Fynwy | Great Oak STW | 2596 | 1039 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.37 | 10.33 | 11.42 | 337916 | 207600 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JL | NP152JL | np15 2jl | np152jl | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 2470 | 995 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.55 | 9.89 | 10.93 | 338934 | 207069 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JP | NP152JP | np15 2jp | np152jp | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 1945 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 339800 | 208304 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JQ | NP152JQ | np15 2jq | np152jq | Monmouthshire | Sir Fynwy | Great Oak STW | 1525 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 338923 | 208751 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JU | NP152JU | np15 2ju | np152ju | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 679 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341504 | 207871 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JW | NP152JW | np15 2jw | np152jw | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 643 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341413 | 207843 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JX | NP152JX | np15 2jx | np152jx | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 763 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341554 | 207947 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JY | NP152JY | np15 2jy | np152jy | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 768 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341583 | 207946 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2JZ | NP152JZ | np15 2jz | np152jz | Monmouthshire | Sir Fynwy | Raglan Enterprise Park | 793 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341690 | 207938 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LA | NP152LA | np15 2la | np152la | Monmouthshire | Sir Fynwy | Raglan STW | 710 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341682 | 207851 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LB | NP152LB | np15 2lb | np152lb | Monmouthshire | Sir Fynwy | Raglan STW | 731 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 341715 | 207870 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LD | NP152LD | np15 2ld | np152ld | Monmouthshire | Sir Fynwy | Raglan STW | 1713 | 952 | 900to1200 | 1.91 | 1.39 | 1.02 | 17.74 | 9.46 | 10.46 | 342419 | 208666 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LH | NP152LH | np15 2lh | np152lh | Monmouthshire | Sir Fynwy | Penrhos STW | 1361 | 944 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.59 | 9.38 | 10.37 | 341786 | 210210 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LN | NP152LN | np15 2ln | np152ln | Monmouthshire | Sir Fynwy | Penrhos STW | 2137 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 342723 | 209789 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LU | NP152LU | np15 2lu | np152lu | Monmouthshire | Sir Fynwy | Llanarth STW | 629 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 337694 | 211099 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LX | NP152LX | np15 2lx | np152lx | Monmouthshire | Sir Fynwy | Llanarth STW | 660 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 337607 | 211113 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LY | NP152LY | np15 2ly | np152ly | Monmouthshire | Sir Fynwy | Llanarth STW | 2006 | 993 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.51 | 9.87 | 10.91 | 338347 | 212401 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LZ | NP152LZ | np15 2lz | np152lz | Monmouthshire | Sir Fynwy | Llanarth STW | 1896 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 337398 | 212333 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2NA | NP152NA | np15 2na | np152na | Monmouthshire | Sir Fynwy | Llanarth STW | 1235 | 1000 | 900to1200 | 2 | 1.46 | 1.07 | 18.64 | 9.94 | 10.99 | 337065 | 211481 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2NB | NP152NB | np15 2nb | np152nb | Monmouthshire | Sir Fynwy | Llanarth STW | 1188 | 993 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.51 | 9.87 | 10.91 | 337541 | 211640 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2YB | NP152YB | np15 2yb | np152yb | Monmouthshire | Sir Fynwy | Llanarth STW | 803 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 337131 | 210009 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2YD | NP152YD | np15 2yd | np152yd | Monmouthshire | Sir Fynwy | Llanarth STW | 292 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 338075 | 210477 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 9AR | NP159AR | np15 9ar | np159ar | Monmouthshire | Sir Fynwy | Usk STW | 1784 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337512 | 200797 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 9AT | NP159AT | np15 9at | np159at | Monmouthshire | Sir Fynwy | Usk STW | 1792 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337507 | 200803 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 9AY | NP159AY | np15 9ay | np159ay | Monmouthshire | Sir Fynwy | Usk STW | 1784 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 337512 | 200797 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 9TA | NP159TA | np15 9ta | np159ta | Monmouthshire | Sir Fynwy | Little Mill STW | 2982 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 336686 | 201883 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 9ZZ | NP159ZZ | np15 9zz | np159zz | Monmouthshire | Sir Fynwy | Little Mill STW | 2982 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 336686 | 201883 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6DA | NP166DA | np16 6da | np166da | Monmouthshire | Sir Fynwy | Devauden STW | 1661 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 346310 | 197505 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6DB | NP166DB | np16 6db | np166db | Monmouthshire | Sir Fynwy | Devauden STW | 1836 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 346005 | 197530 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NB | NP166NB | np16 6nb | np166nb | Monmouthshire | Sir Fynwy | Devauden STW | 1042 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 348287 | 199083 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NN | NP166NN | np16 6nn | np166nn | Monmouthshire | Sir Fynwy | Devauden STW | 1227 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 348414 | 199301 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NR | NP166NR | np16 6nr | np166nr | Monmouthshire | Sir Fynwy | Devauden STW | 1591 | 1076 | 900to1200 | 2.15 | 1.58 | 1.16 | 20.05 | 10.7 | 11.82 | 348016 | 200265 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NS | NP166NS | np16 6ns | np166ns | Monmouthshire | Sir Fynwy | Llanishen STW | 1950 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 347571 | 201142 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NT | NP166NT | np16 6nt | np166nt | Monmouthshire | Sir Fynwy | Llanishen STW | 1198 | 1014 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.9 | 10.08 | 11.14 | 347438 | 201911 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NU | NP166NU | np16 6nu | np166nu | Monmouthshire | Sir Fynwy | Llanishen STW | 1073 | 1014 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.9 | 10.08 | 11.14 | 347066 | 202190 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NW | NP166NW | np16 6nw | np166nw | Monmouthshire | Sir Fynwy | Devauden STW | 1554 | 1076 | 900to1200 | 2.15 | 1.58 | 1.16 | 20.05 | 10.7 | 11.82 | 348038 | 200210 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NX | NP166NX | np16 6nx | np166nx | Monmouthshire | Sir Fynwy | Devauden STW | 1044 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 348313 | 198842 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NY | NP166NY | np16 6ny | np166ny | Monmouthshire | Sir Fynwy | Devauden STW | 1925 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 345481 | 199569 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NZ | NP166NZ | np16 6nz | np166nz | Monmouthshire | Sir Fynwy | Llansoy STW | 2782 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 344394 | 199327 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PA | NP166PA | np16 6pa | np166pa | Monmouthshire | Sir Fynwy | Devauden STW | 1636 | 1076 | 900to1200 | 2.15 | 1.58 | 1.16 | 20.05 | 10.7 | 11.82 | 347598 | 200462 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PB | NP166PB | np16 6pb | np166pb | Monmouthshire | Sir Fynwy | Devauden STW | 934 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 348141 | 199195 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PD | NP166PD | np16 6pd | np166pd | Monmouthshire | Sir Fynwy | Devauden STW | 981 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 346478 | 198281 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PG | NP166PG | np16 6pg | np166pg | Monmouthshire | Sir Fynwy | Devauden STW | 1003 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 348271 | 198913 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PJ | NP166PJ | np16 6pj | np166pj | Monmouthshire | Sir Fynwy | Devauden STW | 975 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 348244 | 198829 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PP | NP166PP | np16 6pp | np166pp | Monmouthshire | Sir Fynwy | Devauden STW | 657 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 347012 | 199464 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PQ | NP166PQ | np16 6pq | np166pq | Monmouthshire | Sir Fynwy | Devauden STW | 1228 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 348498 | 198865 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PR | NP166PR | np16 6pr | np166pr | Monmouthshire | Sir Fynwy | Llansoy STW | 2418 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 344920 | 199897 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PT | NP166PT | np16 6pt | np166pt | Monmouthshire | Sir Fynwy | Devauden STW | 354 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 347218 | 198510 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PZ | NP166PZ | np16 6pz | np166pz | Monmouthshire | Sir Fynwy | Devauden STW | 953 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 348215 | 198978 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QA | NP166QA | np16 6qa | np166qa | Monmouthshire | Sir Fynwy | Devauden STW | 1154 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 348419 | 198958 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QB | NP166QB | np16 6qb | np166qb | Monmouthshire | Sir Fynwy | Llanishen STW | 99 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 347661 | 203188 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QD | NP166QD | np16 6qd | np166qd | Monmouthshire | Sir Fynwy | Llanishen STW | 1022 | 992 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.49 | 9.86 | 10.9 | 346880 | 203761 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QE | NP166QE | np16 6qe | np166qe | Monmouthshire | Sir Fynwy | Llanishen STW | 71 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 347659 | 203160 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QG | NP166QG | np16 6qg | np166qg | Monmouthshire | Sir Fynwy | Llanishen STW | 323 | 1010 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.82 | 10.04 | 11.1 | 347461 | 202828 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QJ | NP166QJ | np16 6qj | np166qj | Monmouthshire | Sir Fynwy | Llanishen STW | 132 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 347736 | 203190 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QL | NP166QL | np16 6ql | np166ql | Monmouthshire | Sir Fynwy | Llanishen STW | 94 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 347614 | 203003 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QS | NP166QS | np16 6qs | np166qs | Monmouthshire | Sir Fynwy | Llanishen STW | 431 | 1010 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.82 | 10.04 | 11.1 | 347359 | 203408 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QT | NP166QT | np16 6qt | np166qt | Monmouthshire | Sir Fynwy | Llanishen STW | 573 | 1010 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.82 | 10.04 | 11.1 | 347206 | 203452 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QU | NP166QU | np16 6qu | np166qu | Monmouthshire | Sir Fynwy | Llanishen STW | 1409 | 992 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.49 | 9.86 | 10.9 | 346700 | 204130 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QX | NP166QX | np16 6qx | np166qx | Monmouthshire | Sir Fynwy | Llanishen STW | 914 | 992 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.49 | 9.86 | 10.9 | 346921 | 203641 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QY | NP166QY | np16 6qy | np166qy | Monmouthshire | Sir Fynwy | Llanishen STW | 2238 | 981 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.28 | 9.75 | 10.78 | 346872 | 205188 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QZ | NP166QZ | np16 6qz | np166qz | Monmouthshire | Sir Fynwy | Llanishen STW | 1437 | 992 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.49 | 9.86 | 10.9 | 347365 | 204498 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1AA | NP181AA | np18 1aa | np181aa | Newport | Casnewydd | Christchurch WwTW | 557 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334043 | 190315 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AB | NP181AB | np18 1ab | np181ab | Newport | Casnewydd | Ponthir STW | 607 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334053 | 190417 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AD | NP181AD | np18 1ad | np181ad | Newport | Casnewydd | Ponthir STW | 550 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334112 | 190382 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AE | NP181AE | np18 1ae | np181ae | Newport | Casnewydd | Ponthir STW | 672 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334000 | 190554 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AF | NP181AF | np18 1af | np181af | Newport | Casnewydd | Ponthir STW | 610 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334065 | 190563 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AG | NP181AG | np18 1ag | np181ag | Newport | Casnewydd | Ponthir STW | 544 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334117 | 190453 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AH | NP181AH | np18 1ah | np181ah | Newport | Casnewydd | Ponthir STW | 559 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334102 | 190465 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AJ | NP181AJ | np18 1aj | np181aj | Newport | Casnewydd | Ponthir STW | 485 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334197 | 190574 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AL | NP181AL | np18 1al | np181al | Newport | Casnewydd | Ponthir STW | 524 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334161 | 190589 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AN | NP181AN | np18 1an | np181an | Newport | Casnewydd | Ponthir STW | 536 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334176 | 190659 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AP | NP181AP | np18 1ap | np181ap | Newport | Casnewydd | Ponthir STW | 582 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334127 | 190662 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AQ | NP181AQ | np18 1aq | np181aq | Newport | Casnewydd | Ponthir STW | 583 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334107 | 190613 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AR | NP181AR | np18 1ar | np181ar | Newport | Casnewydd | Ponthir STW | 660 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334057 | 190698 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AS | NP181AS | np18 1as | np181as | Newport | Casnewydd | Ponthir STW | 655 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334033 | 190619 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AT | NP181AT | np18 1at | np181at | Newport | Casnewydd | Ponthir STW | 712 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334050 | 190797 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AU | NP181AU | np18 1au | np181au | Newport | Casnewydd | Ponthir STW | 739 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333984 | 190728 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AW | NP181AW | np18 1aw | np181aw | Newport | Casnewydd | Ponthir STW | 791 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333921 | 190711 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AX | NP181AX | np18 1ax | np181ax | Newport | Casnewydd | Ponthir STW | 690 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333999 | 190626 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AY | NP181AY | np18 1ay | np181ay | Newport | Casnewydd | Christchurch WwTW | 768 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333838 | 190529 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1AZ | NP181AZ | np18 1az | np181az | Newport | Casnewydd | Ponthir STW | 820 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333869 | 190644 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BA | NP181BA | np18 1ba | np181ba | Newport | Casnewydd | Ponthir STW | 931 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333774 | 190715 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BB | NP181BB | np18 1bb | np181bb | Newport | Casnewydd | Ponthir STW | 773 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333982 | 190801 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BD | NP181BD | np18 1bd | np181bd | Newport | Casnewydd | Ponthir STW | 758 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334007 | 190814 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BE | NP181BE | np18 1be | np181be | Newport | Casnewydd | Ponthir STW | 904 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333893 | 190907 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BG | NP181BG | np18 1bg | np181bg | Newport | Casnewydd | Ponthir STW | 815 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334067 | 190988 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BH | NP181BH | np18 1bh | np181bh | Newport | Casnewydd | Ponthir STW | 782 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334025 | 190886 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BJ | NP181BJ | np18 1bj | np181bj | Newport | Casnewydd | Ponthir STW | 605 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334124 | 190710 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BL | NP181BL | np18 1bl | np181bl | Newport | Casnewydd | Ponthir STW | 528 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334203 | 190695 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BN | NP181BN | np18 1bn | np181bn | Newport | Casnewydd | Ponthir STW | 401 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334259 | 190427 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BP | NP181BP | np18 1bp | np181bp | Newport | Casnewydd | Ponthir STW | 371 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334289 | 190440 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BR | NP181BR | np18 1br | np181br | Newport | Casnewydd | Ponthir STW | 441 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334220 | 190449 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BS | NP181BS | np18 1bs | np181bs | Newport | Casnewydd | Ponthir STW | 365 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334324 | 190571 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BT | NP181BT | np18 1bt | np181bt | Newport | Casnewydd | Ponthir STW | 851 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333847 | 190681 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BU | NP181BU | np18 1bu | np181bu | Newport | Casnewydd | Ponthir STW | 1113 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333687 | 190970 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BW | NP181BW | np18 1bw | np181bw | Newport | Casnewydd | Ponthir STW | 688 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334081 | 190801 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BX | NP181BX | np18 1bx | np181bx | Newport | Casnewydd | Ponthir STW | 847 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333870 | 190734 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BY | NP181BY | np18 1by | np181by | Newport | Casnewydd | Ponthir STW | 354 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334308 | 190468 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1BZ | NP181BZ | np18 1bz | np181bz | Newport | Casnewydd | Ponthir STW | 829 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334027 | 190965 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1DA | NP181DA | np18 1da | np181da | Newport | Casnewydd | Ponthir STW | 584 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334077 | 190454 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1DB | NP181DB | np18 1db | np181db | Newport | Casnewydd | Tredunnock STW | 1644 | 1102 | 900to1200 | 2.21 | 1.61 | 1.18 | 20.54 | 10.95 | 12.11 | 338214 | 192906 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1DD | NP181DD | np18 1dd | np181dd | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 1179 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 333011 | 195991 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1DY | NP181DY | np18 1dy | np181dy | Newport | Casnewydd | Ponthir STW | 748 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333918 | 190526 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1GA | NP181GA | np18 1ga | np181ga | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1358 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 332432 | 192980 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GD | NP181GD | np18 1gd | np181gd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1444 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 332291 | 193207 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GE | NP181GE | np18 1ge | np181ge | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1106 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332876 | 192696 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GF | NP181GF | np18 1gf | np181gf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1088 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332986 | 192607 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GG | NP181GG | np18 1gg | np181gg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1153 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332841 | 192664 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GH | NP181GH | np18 1gh | np181gh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1222 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332815 | 192589 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GJ | NP181GJ | np18 1gj | np181gj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1255 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332811 | 192546 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GL | NP181GL | np18 1gl | np181gl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1238 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332712 | 192692 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GN | NP181GN | np18 1gn | np181gn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1323 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332621 | 192674 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GP | NP181GP | np18 1gp | np181gp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1225 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332702 | 192729 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GQ | NP181GQ | np18 1gq | np181gq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1421 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 332435 | 192804 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GR | NP181GR | np18 1gr | np181gr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1368 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332516 | 192762 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GS | NP181GS | np18 1gs | np181gs | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1364 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 332475 | 192854 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GT | NP181GT | np18 1gt | np181gt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1301 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332569 | 192805 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GU | NP181GU | np18 1gu | np181gu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1243 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332642 | 192792 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GW | NP181GW | np18 1gw | np181gw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1168 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332678 | 192883 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GX | NP181GX | np18 1gx | np181gx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1218 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332633 | 192862 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GY | NP181GY | np18 1gy | np181gy | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1308 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 332452 | 193090 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1GZ | NP181GZ | np18 1gz | np181gz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1311 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 332475 | 193001 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1HA | NP181HA | np18 1ha | np181ha | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1298 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 332444 | 193177 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1HB | NP181HB | np18 1hb | np181hb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1236 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 332489 | 193306 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1HD | NP181HD | np18 1hd | np181hd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1306 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 332427 | 193226 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1HE | NP181HE | np18 1he | np181he | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1345 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 332430 | 193031 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1HF | NP181HF | np18 1hf | np181hf | Newport | Casnewydd | Ponthir STW | 848 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 335273 | 189844 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1HG | NP181HG | np18 1hg | np181hg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1113 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332626 | 193208 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1HH | NP181HH | np18 1hh | np181hh | Newport | Casnewydd | STW Serving Court Farm Wtw | 1273 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333177 | 192259 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1HL | NP181HL | np18 1hl | np181hl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1168 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332614 | 193036 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1HN | NP181HN | np18 1hn | np181hn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1060 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332766 | 192948 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1HP | NP181HP | np18 1hp | np181hp | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 266 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 333743 | 195281 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1HR | NP181HR | np18 1hr | np181hr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 812 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 333076 | 192916 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1HS | NP181HS | np18 1hs | np181hs | Monmouthshire | Sir Fynwy | STW Serving Court Farm Wtw | 73 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 333673 | 193466 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1HT | NP181HT | np18 1ht | np181ht | Monmouthshire | Sir Fynwy | STW Serving Court Farm Wtw | 262 | 1174 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.88 | 11.67 | 12.9 | 333702 | 193671 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1HU | NP181HU | np18 1hu | np181hu | Monmouthshire | Sir Fynwy | STW Serving Court Farm Wtw | 880 | 1194 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.25 | 11.87 | 13.12 | 333047 | 193977 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1HW | NP181HW | np18 1hw | np181hw | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 1011 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 333190 | 194746 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1HX | NP181HX | np18 1hx | np181hx | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 486 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 333574 | 195584 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1HY | NP181HY | np18 1hy | np181hy | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 172 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 334007 | 195522 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1HZ | NP181HZ | np18 1hz | np181hz | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 238 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 334063 | 195579 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1JA | NP181JA | np18 1ja | np181ja | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 281 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 333933 | 195623 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1JB | NP181JB | np18 1jb | np181jb | Newport | Casnewydd | Ponthir STW | 855 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334094 | 191071 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JD | NP181JD | np18 1jd | np181jd | Newport | Casnewydd | Ponthir STW | 1348 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335153 | 189176 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JE | NP181JE | np18 1je | np181je | Newport | Casnewydd | Ponthir STW | 1259 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335152 | 189272 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JF | NP181JF | np18 1jf | np181jf | Newport | Casnewydd | Ponthir STW | 1056 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335105 | 189473 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JG | NP181JG | np18 1jg | np181jg | Newport | Casnewydd | Christchurch WwTW | 641 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 334568 | 189643 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JH | NP181JH | np18 1jh | np181jh | Newport | Casnewydd | Christchurch WwTW | 450 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334373 | 189890 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JJ | NP181JJ | np18 1jj | np181jj | Newport | Casnewydd | Christchurch WwTW | 868 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334679 | 189313 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JL | NP181JL | np18 1jl | np181jl | Newport | Casnewydd | Christchurch WwTW | 662 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334511 | 189434 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JN | NP181JN | np18 1jn | np181jn | Newport | Casnewydd | Christchurch WwTW | 715 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334560 | 189412 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JP | NP181JP | np18 1jp | np181jp | Newport | Casnewydd | Christchurch WwTW | 980 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334797 | 189294 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JQ | NP181JQ | np18 1jq | np181jq | Newport | Casnewydd | Ponthir STW | 2217 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 336843 | 190815 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JS | NP181JS | np18 1js | np181js | Newport | Casnewydd | Tredunnock STW | 1950 | 1102 | 900to1200 | 2.21 | 1.61 | 1.18 | 20.54 | 10.95 | 12.11 | 338197 | 192588 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JT | NP181JT | np18 1jt | np181jt | Newport | Casnewydd | Christchurch WwTW | 474 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334371 | 189965 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JU | NP181JU | np18 1ju | np181ju | Newport | Casnewydd | Christchurch WwTW | 440 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334358 | 189906 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JW | NP181JW | np18 1jw | np181jw | Newport | Casnewydd | Christchurch WwTW | 396 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334320 | 189878 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JX | NP181JX | np18 1jx | np181jx | Newport | Casnewydd | Christchurch WwTW | 427 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334362 | 189832 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1JZ | NP181JZ | np18 1jz | np181jz | Newport | Casnewydd | Christchurch WwTW | 781 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334628 | 189398 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LB | NP181LB | np18 1lb | np181lb | Newport | Casnewydd | Ponthir STW | 615 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 335146 | 190054 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LD | NP181LD | np18 1ld | np181ld | Newport | Casnewydd | Ponthir STW | 1585 | 1123 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.93 | 11.16 | 12.34 | 336124 | 191035 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LE | NP181LE | np18 1le | np181le | Newport | Casnewydd | Ponthir STW | 853 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334044 | 191019 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LF | NP181LF | np18 1lf | np181lf | Newport | Casnewydd | Ponthir STW | 666 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334194 | 190906 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LG | NP181LG | np18 1lg | np181lg | Newport | Casnewydd | Ponthir STW | 818 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334010 | 190926 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LH | NP181LH | np18 1lh | np181lh | Newport | Casnewydd | Ponthir STW | 892 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333954 | 190974 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LJ | NP181LJ | np18 1lj | np181lj | Newport | Casnewydd | Ponthir STW | 1066 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333889 | 191166 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LL | NP181LL | np18 1ll | np181ll | Newport | Casnewydd | Ponthir STW | 1013 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333926 | 191127 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LN | NP181LN | np18 1ln | np181ln | Newport | Casnewydd | Ponthir STW | 878 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333997 | 191005 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LP | NP181LP | np18 1lp | np181lp | Newport | Casnewydd | Ponthir STW | 1088 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 334553 | 191512 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LQ | NP181LQ | np18 1lq | np181lq | Newport | Casnewydd | STW Serving Court Farm Wtw | 922 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 334228 | 192641 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LR | NP181LR | np18 1lr | np181lr | Monmouthshire | Sir Fynwy | STW Serving Court Farm Wtw | 1274 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 334959 | 193115 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1LS | NP181LS | np18 1ls | np181ls | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 1148 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 335039 | 194862 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1LT | NP181LT | np18 1lt | np181lt | Monmouthshire | Sir Fynwy | STW Serving Court Farm Wtw | 1725 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 335408 | 193056 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1LU | NP181LU | np18 1lu | np181lu | Monmouthshire | Sir Fynwy | Tredunnock STW | 2324 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 336341 | 192683 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1LW | NP181LW | np18 1lw | np181lw | Monmouthshire | Sir Fynwy | Tredunnock STW | 2060 | 1146 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.36 | 11.39 | 12.59 | 335762 | 194168 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1LX | NP181LX | np18 1lx | np181lx | Newport | Casnewydd | Ponthir STW | 993 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333984 | 191157 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LY | NP181LY | np18 1ly | np181ly | Newport | Casnewydd | Ponthir STW | 890 | 1095 | 900to1200 | 2.19 | 1.6 | 1.18 | 20.41 | 10.88 | 12.03 | 334530 | 191310 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1LZ | NP181LZ | np18 1lz | np181lz | Newport | Casnewydd | Ponthir STW | 1685 | 1117 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.82 | 11.1 | 12.27 | 335931 | 191535 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NA | NP181NA | np18 1na | np181na | Newport | Casnewydd | Christchurch WwTW | 1080 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333619 | 190799 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NB | NP181NB | np18 1nb | np181nb | Newport | Casnewydd | Christchurch WwTW | 1147 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333567 | 190852 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1ND | NP181ND | np18 1nd | np181nd | Newport | Casnewydd | Ponthir STW | 1077 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333844 | 191133 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NE | NP181NE | np18 1ne | np181ne | Newport | Casnewydd | Ponthir STW | 1082 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333798 | 191083 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NF | NP181NF | np18 1nf | np181nf | Newport | Casnewydd | Ponthir STW | 1008 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333704 | 190748 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NG | NP181NG | np18 1ng | np181ng | Newport | Casnewydd | Ponthir STW | 948 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333810 | 190849 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NH | NP181NH | np18 1nh | np181nh | Newport | Casnewydd | Ponthir STW | 970 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333852 | 190966 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NJ | NP181NJ | np18 1nj | np181nj | Newport | Casnewydd | Ponthir STW | 1060 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333762 | 190993 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NL | NP181NL | np18 1nl | np181nl | Newport | Casnewydd | Ponthir STW | 1017 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333872 | 191072 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NP | NP181NP | np18 1np | np181np | Newport | Casnewydd | Ponthir STW | 1016 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333773 | 190925 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NQ | NP181NQ | np18 1nq | np181nq | Newport | Casnewydd | Ponthir STW | 989 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333783 | 190887 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NR | NP181NR | np18 1nr | np181nr | Newport | Casnewydd | Ponthir STW | 1063 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333721 | 190928 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NS | NP181NS | np18 1ns | np181ns | Newport | Casnewydd | Ponthir STW | 627 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334165 | 190815 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NT | NP181NT | np18 1nt | np181nt | Newport | Casnewydd | Ponthir STW | 928 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334130 | 191191 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1NU | NP181NU | np18 1nu | np181nu | Monmouthshire | Sir Fynwy | STW Serving Court Farm Wtw | 1006 | 1125 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.97 | 11.18 | 12.36 | 334618 | 193863 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP18 1NX | NP181NX | np18 1nx | np181nx | Newport | Casnewydd | Ponthir STW | 910 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334014 | 191071 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1PA | NP181PA | np18 1pa | np181pa | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1075 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 333032 | 192584 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1PB | NP181PB | np18 1pb | np181pb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1052 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332995 | 192648 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1PD | NP181PD | np18 1pd | np181pd | Newport | Casnewydd | STW Serving Court Farm Wtw | 1191 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333092 | 192399 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1PE | NP181PE | np18 1pe | np181pe | Newport | Casnewydd | STW Serving Court Farm Wtw | 1269 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333174 | 192265 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1PF | NP181PF | np18 1pf | np181pf | Newport | Casnewydd | STW Serving Court Farm Wtw | 1231 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333146 | 192322 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1PG | NP181PG | np18 1pg | np181pg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1006 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 333097 | 192620 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1PH | NP181PH | np18 1ph | np181ph | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1026 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 333075 | 192613 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1PJ | NP181PJ | np18 1pj | np181pj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1025 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 333060 | 192626 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1PL | NP181PL | np18 1pl | np181pl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1038 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332995 | 192667 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1PN | NP181PN | np18 1pn | np181pn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1138 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332769 | 192785 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1PP | NP181PP | np18 1pp | np181pp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1206 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332604 | 192953 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1PQ | NP181PQ | np18 1pq | np181pq | Newport | Casnewydd | STW Serving Court Farm Wtw | 1254 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333365 | 192208 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1PR | NP181PR | np18 1pr | np181pr | Newport | Casnewydd | STW Serving Court Farm Wtw | 1246 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333050 | 192360 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1PY | NP181PY | np18 1py | np181py | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1132 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332827 | 192715 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1PZ | NP181PZ | np18 1pz | np181pz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1045 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 333083 | 192582 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1QA | NP181QA | np18 1qa | np181qa | Newport | Casnewydd | Caerleon Road STW | 103 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 333800 | 189595 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QB | NP181QB | np18 1qb | np181qb | Newport | Casnewydd | Christchurch WwTW | 485 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334187 | 190185 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QD | NP181QD | np18 1qd | np181qd | Newport | Casnewydd | Ponthir STW | 434 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334227 | 190402 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QE | NP181QE | np18 1qe | np181qe | Newport | Casnewydd | Ponthir STW | 457 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334249 | 190230 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QF | NP181QF | np18 1qf | np181qf | Newport | Casnewydd | Christchurch WwTW | 502 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334208 | 190192 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QG | NP181QG | np18 1qg | np181qg | Newport | Casnewydd | Ponthir STW | 359 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334416 | 190167 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QH | NP181QH | np18 1qh | np181qh | Newport | Casnewydd | Ponthir STW | 431 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334258 | 190275 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QJ | NP181QJ | np18 1qj | np181qj | Newport | Casnewydd | Ponthir STW | 400 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334311 | 190235 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QL | NP181QL | np18 1ql | np181ql | Newport | Casnewydd | Ponthir STW | 374 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334362 | 190205 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QP | NP181QP | np18 1qp | np181qp | Newport | Casnewydd | Ponthir STW | 384 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 334494 | 190084 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QQ | NP181QQ | np18 1qq | np181qq | Newport | Casnewydd | Ponthir STW | 371 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 334562 | 190072 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QR | NP181QR | np18 1qr | np181qr | Newport | Casnewydd | Ponthir STW | 1574 | 1123 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.93 | 11.16 | 12.34 | 335871 | 191435 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QS | NP181QS | np18 1qs | np181qs | Newport | Casnewydd | Ponthir STW | 1073 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333680 | 190867 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1QW | NP181QW | np18 1qw | np181qw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1094 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332672 | 193097 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1RE | NP181RE | np18 1re | np181re | Newport | Casnewydd | Ponthir STW | 737 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 334012 | 190781 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 1RY | NP181RY | np18 1ry | np181ry | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1023 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 332946 | 192741 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1TN | NP181TN | np18 1tn | np181tn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1201 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 332944 | 192494 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP18 1YE | NP181YE | np18 1ye | np181ye | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2BS | NP182BS | np18 2bs | np182bs | Newport | Casnewydd | Nash STW | 1795 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 334237 | 185723 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2BT | NP182BT | np18 2bt | np182bt | Newport | Casnewydd | Nash STW | 1512 | 986 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.38 | 9.8 | 10.83 | 334534 | 185163 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2BU | NP182BU | np18 2bu | np182bu | Newport | Casnewydd | Nash STW | 1332 | 970 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.08 | 9.64 | 10.66 | 334318 | 185120 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2DB | NP182DB | np18 2db | np182db | Newport | Casnewydd | Caerleon Road STW | 2406 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335179 | 187618 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2DJ | NP182DJ | np18 2dj | np182dj | Newport | Casnewydd | Ponthir STW | 2719 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 336241 | 188219 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2EF | NP182EF | np18 2ef | np182ef | Newport | Casnewydd | Ponthir STW | 2534 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 336254 | 188461 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2EH | NP182EH | np18 2eh | np182eh | Newport | Casnewydd | Ponthir STW | 2582 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 336271 | 188413 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2EJ | NP182EJ | np18 2ej | np182ej | Newport | Casnewydd | Ponthir STW | 2562 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 336325 | 188484 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2EP | NP182EP | np18 2ep | np182ep | Newport | Casnewydd | Nash STW | 1456 | 970 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.08 | 9.64 | 10.66 | 334434 | 185183 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2LL | NP182LL | np18 2ll | np182ll | Newport | Casnewydd | Caerleon Road STW | 2441 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335237 | 187619 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2LN | NP182LN | np18 2ln | np182ln | Newport | Casnewydd | Caerleon Road STW | 2378 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335266 | 187724 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2LP | NP182LP | np18 2lp | np182lp | Newport | Casnewydd | Ponthir STW | 1352 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335283 | 189231 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2LR | NP182LR | np18 2lr | np182lr | Newport | Casnewydd | Ponthir STW | 1311 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335404 | 189351 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2LS | NP182LS | np18 2ls | np182ls | Newport | Casnewydd | Ponthir STW | 1369 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335503 | 189352 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2NH | NP182NH | np18 2nh | np182nh | Newport | Casnewydd | Caerleon Road STW | 2567 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335468 | 187652 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2TA | NP182TA | np18 2ta | np182ta | Newport | Casnewydd | Ponthir STW | 1774 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 336162 | 189488 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2YB | NP182YB | np18 2yb | np182yb | Newport | Casnewydd | Ponthir STW | 1407 | 1111 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.71 | 11.04 | 12.21 | 335745 | 189535 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2YE | NP182YE | np18 2ye | np182ye | Newport | Casnewydd | Caerleon Road STW | 2449 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335530 | 187882 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 2YG | NP182YG | np18 2yg | np182yg | Newport | Casnewydd | Ponthir STW | 1617 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335894 | 189386 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3AB | NP183AB | np18 3ab | np183ab | Newport | Casnewydd | Ponthir STW | 1444 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333509 | 191301 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3BS | NP183BS | np18 3bs | np183bs | Newport | Casnewydd | Christchurch WwTW | 1816 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333026 | 191336 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3BT | NP183BT | np18 3bt | np183bt | Newport | Casnewydd | Christchurch WwTW | 1845 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333033 | 191374 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3BU | NP183BU | np18 3bu | np183bu | Newport | Casnewydd | Christchurch WwTW | 1870 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332987 | 191376 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3BW | NP183BW | np18 3bw | np183bw | Newport | Casnewydd | STW Serving Court Farm Wtw | 2011 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 332847 | 191599 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3BX | NP183BX | np18 3bx | np183bx | Newport | Casnewydd | Christchurch WwTW | 1840 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332843 | 191244 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3BY | NP183BY | np18 3by | np183by | Newport | Casnewydd | Christchurch WwTW | 1966 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332718 | 191307 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3BZ | NP183BZ | np18 3bz | np183bz | Newport | Casnewydd | Christchurch WwTW | 2094 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332592 | 191369 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DA | NP183DA | np18 3da | np183da | Newport | Casnewydd | Christchurch WwTW | 1638 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333060 | 191149 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DB | NP183DB | np18 3db | np183db | Newport | Casnewydd | Christchurch WwTW | 1726 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332865 | 191117 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DD | NP183DD | np18 3dd | np183dd | Newport | Casnewydd | Christchurch WwTW | 1704 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332863 | 191088 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DE | NP183DE | np18 3de | np183de | Newport | Casnewydd | Christchurch WwTW | 1752 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332877 | 191160 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DF | NP183DF | np18 3df | np183df | Newport | Casnewydd | Christchurch WwTW | 1824 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332918 | 191278 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DG | NP183DG | np18 3dg | np183dg | Newport | Casnewydd | Christchurch WwTW | 1864 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332896 | 191311 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DH | NP183DH | np18 3dh | np183dh | Newport | Casnewydd | Christchurch WwTW | 1874 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332925 | 191342 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DJ | NP183DJ | np18 3dj | np183dj | Newport | Casnewydd | Christchurch WwTW | 1837 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332772 | 191185 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DL | NP183DL | np18 3dl | np183dl | Newport | Casnewydd | Christchurch WwTW | 2021 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332659 | 191330 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DN | NP183DN | np18 3dn | np183dn | Newport | Casnewydd | Christchurch WwTW | 1934 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332682 | 191236 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DP | NP183DP | np18 3dp | np183dp | Newport | Casnewydd | Christchurch WwTW | 1981 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332634 | 191257 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DQ | NP183DQ | np18 3dq | np183dq | Newport | Casnewydd | Christchurch WwTW | 1974 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332833 | 191402 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DR | NP183DR | np18 3dr | np183dr | Newport | Casnewydd | Christchurch WwTW | 1942 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332850 | 191374 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DS | NP183DS | np18 3ds | np183ds | Newport | Casnewydd | Christchurch WwTW | 2038 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332772 | 191437 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DT | NP183DT | np18 3dt | np183dt | Newport | Casnewydd | Christchurch WwTW | 2065 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332732 | 191442 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DU | NP183DU | np18 3du | np183du | Newport | Casnewydd | STW Serving Court Farm Wtw | 2120 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 332729 | 191537 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DW | NP183DW | np18 3dw | np183dw | Newport | Casnewydd | STW Serving Court Farm Wtw | 2020 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 332752 | 191638 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DX | NP183DX | np18 3dx | np183dx | Newport | Casnewydd | STW Serving Court Farm Wtw | 1984 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 332919 | 191596 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DY | NP183DY | np18 3dy | np183dy | Newport | Casnewydd | Christchurch WwTW | 1847 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332974 | 191342 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3DZ | NP183DZ | np18 3dz | np183dz | Newport | Casnewydd | Christchurch WwTW | 2123 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332664 | 191464 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EA | NP183EA | np18 3ea | np183ea | Newport | Casnewydd | Christchurch WwTW | 2152 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332592 | 191445 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EB | NP183EB | np18 3eb | np183eb | Newport | Casnewydd | Christchurch WwTW | 2057 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332664 | 191380 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3ED | NP183ED | np18 3ed | np183ed | Newport | Casnewydd | Christchurch WwTW | 2169 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 332660 | 191518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EE | NP183EE | np18 3ee | np183ee | Newport | Casnewydd | STW Serving Court Farm Wtw | 2177 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 332609 | 191539 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EF | NP183EF | np18 3ef | np183ef | Newport | Casnewydd | STW Serving Court Farm Wtw | 2139 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 332634 | 191568 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EG | NP183EG | np18 3eg | np183eg | Newport | Casnewydd | Christchurch WwTW | 2204 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332561 | 191486 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EH | NP183EH | np18 3eh | np183eh | Newport | Casnewydd | Christchurch WwTW | 1580 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333164 | 191144 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EJ | NP183EJ | np18 3ej | np183ej | Newport | Casnewydd | Christchurch WwTW | 1672 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333120 | 191225 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EL | NP183EL | np18 3el | np183el | Newport | Casnewydd | Ponthir STW | 1710 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333231 | 191368 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EN | NP183EN | np18 3en | np183en | Newport | Casnewydd | Ponthir STW | 1636 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333248 | 191255 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EP | NP183EP | np18 3ep | np183ep | Newport | Casnewydd | Ponthir STW | 1701 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333324 | 191482 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EQ | NP183EQ | np18 3eq | np183eq | Newport | Casnewydd | Ponthir STW | 1693 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333284 | 191416 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3ER | NP183ER | np18 3er | np183er | Newport | Casnewydd | Ponthir STW | 1786 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333254 | 191530 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3ES | NP183ES | np18 3es | np183es | Newport | Casnewydd | Ponthir STW | 1849 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333185 | 191544 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3ET | NP183ET | np18 3et | np183et | Newport | Casnewydd | Ponthir STW | 1879 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333165 | 191567 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EU | NP183EU | np18 3eu | np183eu | Newport | Casnewydd | STW Serving Court Farm Wtw | 1845 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333207 | 191638 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EW | NP183EW | np18 3ew | np183ew | Newport | Casnewydd | STW Serving Court Farm Wtw | 1807 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333128 | 191703 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EX | NP183EX | np18 3ex | np183ex | Newport | Casnewydd | STW Serving Court Farm Wtw | 2000 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 332986 | 191550 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EY | NP183EY | np18 3ey | np183ey | Newport | Casnewydd | STW Serving Court Farm Wtw | 1889 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333137 | 191614 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3EZ | NP183EZ | np18 3ez | np183ez | Newport | Casnewydd | STW Serving Court Farm Wtw | 1902 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 332951 | 191671 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FA | NP183FA | np18 3fa | np183fa | Newport | Casnewydd | STW Serving Court Farm Wtw | 1795 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333075 | 191736 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FB | NP183FB | np18 3fb | np183fb | Newport | Casnewydd | Christchurch WwTW | 1934 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332936 | 191420 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FD | NP183FD | np18 3fd | np183fd | Newport | Casnewydd | Christchurch WwTW | 1866 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333042 | 191403 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FE | NP183FE | np18 3fe | np183fe | Newport | Casnewydd | Christchurch WwTW | 1856 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333080 | 191412 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FF | NP183FF | np18 3ff | np183ff | Newport | Casnewydd | Ponthir STW | 1871 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333092 | 191449 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FG | NP183FG | np18 3fg | np183fg | Newport | Casnewydd | Ponthir STW | 1841 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333130 | 191452 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FH | NP183FH | np18 3fh | np183fh | Newport | Casnewydd | Ponthir STW | 1811 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333175 | 191465 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FJ | NP183FJ | np18 3fj | np183fj | Newport | Casnewydd | Ponthir STW | 1808 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333132 | 191395 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FL | NP183FL | np18 3fl | np183fl | Newport | Casnewydd | Ponthir STW | 1779 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333172 | 191404 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FN | NP183FN | np18 3fn | np183fn | Newport | Casnewydd | Ponthir STW | 1859 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333148 | 191510 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FP | NP183FP | np18 3fp | np183fp | Newport | Casnewydd | Ponthir STW | 1818 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333182 | 191487 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FQ | NP183FQ | np18 3fq | np183fq | Newport | Casnewydd | Ponthir STW | 1789 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333302 | 191594 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FR | NP183FR | np18 3fr | np183fr | Newport | Casnewydd | Ponthir STW | 1750 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333337 | 191574 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FS | NP183FS | np18 3fs | np183fs | Newport | Casnewydd | Christchurch WwTW | 1919 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332998 | 191439 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FT | NP183FT | np18 3ft | np183ft | Newport | Casnewydd | Ponthir STW | 1934 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333064 | 191521 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FU | NP183FU | np18 3fu | np183fu | Newport | Casnewydd | STW Serving Court Farm Wtw | 1781 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333260 | 191690 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FW | NP183FW | np18 3fw | np183fw | Newport | Casnewydd | STW Serving Court Farm Wtw | 1759 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333194 | 191732 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FX | NP183FX | np18 3fx | np183fx | Newport | Casnewydd | STW Serving Court Farm Wtw | 1750 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333388 | 191692 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FY | NP183FY | np18 3fy | np183fy | Newport | Casnewydd | STW Serving Court Farm Wtw | 1748 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333269 | 191722 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3FZ | NP183FZ | np18 3fz | np183fz | Newport | Casnewydd | STW Serving Court Farm Wtw | 1745 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333138 | 191766 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3NN | NP183NN | np18 3nn | np183nn | Newport | Casnewydd | Ponthir STW | 1569 | 1131 | 900to1200 | 2.26 | 1.66 | 1.21 | 21.08 | 11.24 | 12.43 | 333696 | 191667 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3NR | NP183NR | np18 3nr | np183nr | Newport | Casnewydd | Ponthir STW | 1385 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333547 | 191254 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3NS | NP183NS | np18 3ns | np183ns | Newport | Casnewydd | Ponthir STW | 1188 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333643 | 191044 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3NT | NP183NT | np18 3nt | np183nt | Newport | Casnewydd | Ponthir STW | 1396 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333519 | 191233 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3NU | NP183NU | np18 3nu | np183nu | Newport | Casnewydd | Ponthir STW | 1252 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333554 | 191016 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3NW | NP183NW | np18 3nw | np183nw | Newport | Casnewydd | Ponthir STW | 1227 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333700 | 191194 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3NX | NP183NX | np18 3nx | np183nx | Newport | Casnewydd | Ponthir STW | 1473 | 1131 | 900to1200 | 2.26 | 1.66 | 1.21 | 21.08 | 11.24 | 12.43 | 333651 | 191502 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3NY | NP183NY | np18 3ny | np183ny | Newport | Casnewydd | STW Serving Court Farm Wtw | 1516 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333431 | 191922 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3NZ | NP183NZ | np18 3nz | np183nz | Newport | Casnewydd | STW Serving Court Farm Wtw | 1636 | 1131 | 900to1200 | 2.26 | 1.66 | 1.21 | 21.08 | 11.24 | 12.43 | 333517 | 191787 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3PA | NP183PA | np18 3pa | np183pa | Newport | Casnewydd | STW Serving Court Farm Wtw | 1439 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333401 | 192007 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3PB | NP183PB | np18 3pb | np183pb | Newport | Casnewydd | STW Serving Court Farm Wtw | 2539 | 1155 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.53 | 11.48 | 12.69 | 331888 | 191653 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3PD | NP183PD | np18 3pd | np183pd | Newport | Casnewydd | STW Serving Court Farm Wtw | 1633 | 1131 | 900to1200 | 2.26 | 1.66 | 1.21 | 21.08 | 11.24 | 12.43 | 333627 | 191780 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3PE | NP183PE | np18 3pe | np183pe | Newport | Casnewydd | STW Serving Court Farm Wtw | 1542 | 1131 | 900to1200 | 2.26 | 1.66 | 1.21 | 21.08 | 11.24 | 12.43 | 333530 | 191880 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3PF | NP183PF | np18 3pf | np183pf | Newport | Casnewydd | STW Serving Court Farm Wtw | 1565 | 1131 | 900to1200 | 2.26 | 1.66 | 1.21 | 21.08 | 11.24 | 12.43 | 333645 | 191847 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3PG | NP183PG | np18 3pg | np183pg | Newport | Casnewydd | STW Serving Court Farm Wtw | 1533 | 1131 | 900to1200 | 2.26 | 1.66 | 1.21 | 21.08 | 11.24 | 12.43 | 333585 | 191883 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3PR | NP183PR | np18 3pr | np183pr | Newport | Casnewydd | Ponthir STW | 1585 | 1131 | 900to1200 | 2.26 | 1.66 | 1.21 | 21.08 | 11.24 | 12.43 | 333550 | 191560 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3PS | NP183PS | np18 3ps | np183ps | Newport | Casnewydd | Ponthir STW | 1265 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333772 | 191331 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3PT | NP183PT | np18 3pt | np183pt | Newport | Casnewydd | Ponthir STW | 1281 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333803 | 191382 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3PU | NP183PU | np18 3pu | np183pu | Newport | Casnewydd | Ponthir STW | 1346 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333783 | 191451 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3PW | NP183PW | np18 3pw | np183pw | Newport | Casnewydd | Ponthir STW | 1444 | 1131 | 900to1200 | 2.26 | 1.66 | 1.21 | 21.08 | 11.24 | 12.43 | 333787 | 191580 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3PX | NP183PX | np18 3px | np183px | Newport | Casnewydd | Ponthir STW | 1408 | 1131 | 900to1200 | 2.26 | 1.66 | 1.21 | 21.08 | 11.24 | 12.43 | 333751 | 191505 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3QQ | NP183QQ | np18 3qq | np183qq | Newport | Casnewydd | Christchurch WwTW | 1519 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333225 | 191108 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3QR | NP183QR | np18 3qr | np183qr | Newport | Casnewydd | Christchurch WwTW | 1436 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333385 | 191092 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3QU | NP183QU | np18 3qu | np183qu | Newport | Casnewydd | Ponthir STW | 1585 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333289 | 191224 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3QW | NP183QW | np18 3qw | np183qw | Newport | Casnewydd | Christchurch WwTW | 1742 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332728 | 191018 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3QX | NP183QX | np18 3qx | np183qx | Newport | Casnewydd | Christchurch WwTW | 1601 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333011 | 191071 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3QY | NP183QY | np18 3qy | np183qy | Newport | Casnewydd | Christchurch WwTW | 1759 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332673 | 190988 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3QZ | NP183QZ | np18 3qz | np183qz | Newport | Casnewydd | Caerleon Road STW | 2477 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 331574 | 190765 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RA | NP183RA | np18 3ra | np183ra | Newport | Casnewydd | Christchurch WwTW | 1551 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333267 | 191165 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RB | NP183RB | np18 3rb | np183rb | Newport | Casnewydd | Caerleon Road STW | 1615 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332570 | 190663 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RD | NP183RD | np18 3rd | np183rd | Newport | Casnewydd | Caerleon Road STW | 1589 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332634 | 190689 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RF | NP183RF | np18 3rf | np183rf | Newport | Casnewydd | Christchurch WwTW | 1570 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332726 | 190762 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RG | NP183RG | np18 3rg | np183rg | Newport | Casnewydd | Caerleon Road STW | 1699 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332435 | 190641 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RH | NP183RH | np18 3rh | np183rh | Newport | Casnewydd | Caerleon Road STW | 1835 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332340 | 190739 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RJ | NP183RJ | np18 3rj | np183rj | Newport | Casnewydd | Caerleon Road STW | 1866 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332284 | 190721 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RL | NP183RL | np18 3rl | np183rl | Newport | Casnewydd | Caerleon Road STW | 1666 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332493 | 190656 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RN | NP183RN | np18 3rn | np183rn | Newport | Casnewydd | Caerleon Road STW | 1955 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332135 | 190674 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RP | NP183RP | np18 3rp | np183rp | Newport | Casnewydd | Caerleon Road STW | 1856 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332195 | 190587 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RQ | NP183RQ | np18 3rq | np183rq | Newport | Casnewydd | Caerleon Road STW | 1908 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332221 | 190709 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RR | NP183RR | np18 3rr | np183rr | Newport | Casnewydd | Caerleon Road STW | 1807 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332261 | 190595 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RS | NP183RS | np18 3rs | np183rs | Newport | Casnewydd | Caerleon Road STW | 1770 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332313 | 190603 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RT | NP183RT | np18 3rt | np183rt | Newport | Casnewydd | Caerleon Road STW | 1765 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332347 | 190638 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RU | NP183RU | np18 3ru | np183ru | Newport | Casnewydd | Caerleon Road STW | 1912 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332264 | 190769 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RW | NP183RW | np18 3rw | np183rw | Newport | Casnewydd | Caerleon Road STW | 1816 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332307 | 190669 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3RX | NP183RX | np18 3rx | np183rx | Newport | Casnewydd | Caerleon Road STW | 2004 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332116 | 190730 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SA | NP183SA | np18 3sa | np183sa | Newport | Casnewydd | Christchurch WwTW | 1764 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332551 | 190854 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SB | NP183SB | np18 3sb | np183sb | Newport | Casnewydd | Caerleon Road STW | 1817 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332449 | 190828 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SD | NP183SD | np18 3sd | np183sd | Newport | Casnewydd | Caerleon Road STW | 1766 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332467 | 190774 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SE | NP183SE | np18 3se | np183se | Newport | Casnewydd | Christchurch WwTW | 1701 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332596 | 190810 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SF | NP183SF | np18 3sf | np183sf | Newport | Casnewydd | Christchurch WwTW | 1670 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332739 | 190927 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SG | NP183SG | np18 3sg | np183sg | Newport | Casnewydd | Christchurch WwTW | 1677 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332655 | 190844 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SH | NP183SH | np18 3sh | np183sh | Newport | Casnewydd | Christchurch WwTW | 1604 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332738 | 190830 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SJ | NP183SJ | np18 3sj | np183sj | Newport | Casnewydd | Christchurch WwTW | 1738 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332647 | 190928 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SL | NP183SL | np18 3sl | np183sl | Newport | Casnewydd | STW Serving Court Farm Wtw | 1399 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333207 | 192109 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SN | NP183SN | np18 3sn | np183sn | Newport | Casnewydd | Caerleon Road STW | 1638 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332610 | 190734 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SP | NP183SP | np18 3sp | np183sp | Newport | Casnewydd | Ponthir STW | 1342 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333602 | 191255 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SQ | NP183SQ | np18 3sq | np183sq | Newport | Casnewydd | Caerleon Road STW | 1751 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332451 | 190735 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SS | NP183SS | np18 3ss | np183ss | Newport | Casnewydd | Christchurch WwTW | 1981 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332385 | 190995 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3ST | NP183ST | np18 3st | np183st | Newport | Casnewydd | Christchurch WwTW | 2056 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332566 | 191297 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SU | NP183SU | np18 3su | np183su | Newport | Casnewydd | Christchurch WwTW | 1914 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332584 | 191118 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SW | NP183SW | np18 3sw | np183sw | Newport | Casnewydd | Caerleon Road STW | 2140 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332252 | 191086 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SX | NP183SX | np18 3sx | np183sx | Newport | Casnewydd | Caerleon Road STW | 2177 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332147 | 191034 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SY | NP183SY | np18 3sy | np183sy | Newport | Casnewydd | Caerleon Road STW | 2060 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332318 | 191039 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3SZ | NP183SZ | np18 3sz | np183sz | Newport | Casnewydd | Christchurch WwTW | 1855 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 332670 | 191119 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3TA | NP183TA | np18 3ta | np183ta | Newport | Casnewydd | Christchurch WwTW | 1907 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 332444 | 190950 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3TB | NP183TB | np18 3tb | np183tb | Newport | Casnewydd | STW Serving Court Farm Wtw | 1707 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333472 | 191722 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3TD | NP183TD | np18 3td | np183td | Newport | Casnewydd | Ponthir STW | 1752 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333430 | 191677 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3TE | NP183TE | np18 3te | np183te | Newport | Casnewydd | STW Serving Court Farm Wtw | 1578 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333356 | 191875 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3TF | NP183TF | np18 3tf | np183tf | Newport | Casnewydd | STW Serving Court Farm Wtw | 1549 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333382 | 191899 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3TG | NP183TG | np18 3tg | np183tg | Newport | Casnewydd | STW Serving Court Farm Wtw | 1586 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333440 | 191849 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3TH | NP183TH | np18 3th | np183th | Newport | Casnewydd | STW Serving Court Farm Wtw | 1647 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333328 | 191811 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3TJ | NP183TJ | np18 3tj | np183tj | Newport | Casnewydd | Ponthir STW | 1646 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 333465 | 191561 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3TN | NP183TN | np18 3tn | np183tn | Newport | Casnewydd | Ponthir STW | 1419 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333573 | 191342 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3XL | NP183XL | np18 3xl | np183xl | Newport | Casnewydd | Ponthir STW | 1614 | 1131 | 900to1200 | 2.26 | 1.66 | 1.21 | 21.08 | 11.24 | 12.43 | 333617 | 191661 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP18 3XQ | NP183XQ | np18 3xq | np183xq | Newport | Casnewydd | Christchurch WwTW | 1398 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 333158 | 190926 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AB | NP190AB | np19 0ab | np190ab | Newport | Casnewydd | Caerleon Road STW | 2434 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331534 | 188462 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AD | NP190AD | np19 0ad | np190ad | Newport | Casnewydd | Caerleon Road STW | 2597 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331400 | 188366 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AE | NP190AE | np19 0ae | np190ae | Newport | Casnewydd | Caerleon Road STW | 2516 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331441 | 188465 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AG | NP190AG | np19 0ag | np190ag | Newport | Casnewydd | Caerleon Road STW | 2481 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331471 | 188485 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AH | NP190AH | np19 0ah | np190ah | Newport | Casnewydd | Caerleon Road STW | 2453 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331504 | 188481 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AJ | NP190AJ | np19 0aj | np190aj | Newport | Casnewydd | Caerleon Road STW | 2398 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331601 | 188409 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AL | NP190AL | np19 0al | np190al | Newport | Casnewydd | Caerleon Road STW | 2463 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331497 | 188472 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AN | NP190AN | np19 0an | np190an | Newport | Casnewydd | Caerleon Road STW | 2512 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331472 | 188411 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AP | NP190AP | np19 0ap | np190ap | Newport | Casnewydd | Caerleon Road STW | 2548 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331585 | 188141 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AQ | NP190AQ | np19 0aq | np190aq | Newport | Casnewydd | Caerleon Road STW | 2585 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331537 | 188148 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AR | NP190AR | np19 0ar | np190ar | Newport | Casnewydd | Caerleon Road STW | 2431 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331557 | 188422 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AS | NP190AS | np19 0as | np190as | Newport | Casnewydd | Caerleon Road STW | 2494 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331502 | 188391 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AT | NP190AT | np19 0at | np190at | Newport | Casnewydd | Caerleon Road STW | 2434 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331557 | 188416 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AU | NP190AU | np19 0au | np190au | Newport | Casnewydd | Caerleon Road STW | 2470 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331558 | 188338 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AW | NP190AW | np19 0aw | np190aw | Newport | Casnewydd | Caerleon Road STW | 2426 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331615 | 188326 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AX | NP190AX | np19 0ax | np190ax | Newport | Casnewydd | Caerleon Road STW | 2409 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331674 | 188259 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AY | NP190AY | np19 0ay | np190ay | Newport | Casnewydd | Caerleon Road STW | 2382 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331677 | 188307 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0AZ | NP190AZ | np19 0az | np190az | Newport | Casnewydd | Caerleon Road STW | 2315 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331720 | 188366 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BA | NP190BA | np19 0ba | np190ba | Newport | Casnewydd | Caerleon Road STW | 2337 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331692 | 188371 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BB | NP190BB | np19 0bb | np190bb | Newport | Casnewydd | Caerleon Road STW | 2609 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331553 | 188078 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BD | NP190BD | np19 0bd | np190bd | Newport | Casnewydd | Caerleon Road STW | 2579 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331637 | 188011 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BE | NP190BE | np19 0be | np190be | Newport | Casnewydd | Caerleon Road STW | 2189 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332358 | 187817 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BG | NP190BG | np19 0bg | np190bg | Newport | Casnewydd | Caerleon Road STW | 2330 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331824 | 188177 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BH | NP190BH | np19 0bh | np190bh | Newport | Casnewydd | Caerleon Road STW | 2379 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331779 | 188156 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BJ | NP190BJ | np19 0bj | np190bj | Newport | Casnewydd | Caerleon Road STW | 2279 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332018 | 188016 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BL | NP190BL | np19 0bl | np190bl | Newport | Casnewydd | Caerleon Road STW | 2214 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331933 | 188224 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BN | NP190BN | np19 0bn | np190bn | Newport | Casnewydd | Caerleon Road STW | 2145 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332049 | 188187 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BP | NP190BP | np19 0bp | np190bp | Newport | Casnewydd | Caerleon Road STW | 2192 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332029 | 188137 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BQ | NP190BQ | np19 0bq | np190bq | Newport | Casnewydd | Caerleon Road STW | 2215 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331971 | 188172 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BR | NP190BR | np19 0br | np190br | Newport | Casnewydd | Caerleon Road STW | 2259 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331960 | 188115 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BS | NP190BS | np19 0bs | np190bs | Newport | Casnewydd | Caerleon Road STW | 2294 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331840 | 188216 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BT | NP190BT | np19 0bt | np190bt | Newport | Casnewydd | Caerleon Road STW | 2229 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331840 | 188334 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BU | NP190BU | np19 0bu | np190bu | Newport | Casnewydd | Caerleon Road STW | 2277 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331791 | 188321 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BW | NP190BW | np19 0bw | np190bw | Newport | Casnewydd | Caerleon Road STW | 2208 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331895 | 188288 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BX | NP190BX | np19 0bx | np190bx | Newport | Casnewydd | Caerleon Road STW | 2129 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331958 | 188337 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BY | NP190BY | np19 0by | np190by | Newport | Casnewydd | Caerleon Road STW | 2093 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332064 | 188252 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0BZ | NP190BZ | np19 0bz | np190bz | Newport | Casnewydd | Caerleon Road STW | 2167 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332085 | 188109 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DA | NP190DA | np19 0da | np190da | Newport | Casnewydd | Caerleon Road STW | 2028 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332192 | 188198 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DB | NP190DB | np19 0db | np190db | Newport | Casnewydd | Caerleon Road STW | 2154 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332117 | 188092 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DE | NP190DE | np19 0de | np190de | Newport | Casnewydd | Caerleon Road STW | 2150 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332135 | 188078 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DF | NP190DF | np19 0df | np190df | Newport | Casnewydd | Caerleon Road STW | 2471 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332143 | 187629 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DG | NP190DG | np19 0dg | np190dg | Newport | Casnewydd | Caerleon Road STW | 2499 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332229 | 187526 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DH | NP190DH | np19 0dh | np190dh | Newport | Casnewydd | Caerleon Road STW | 2523 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332084 | 187610 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DJ | NP190DJ | np19 0dj | np190dj | Newport | Casnewydd | Caerleon Road STW | 2472 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332199 | 187582 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DL | NP190DL | np19 0dl | np190dl | Newport | Casnewydd | Caerleon Road STW | 2306 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332004 | 187990 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DN | NP190DN | np19 0dn | np190dn | Newport | Casnewydd | Caerleon Road STW | 2396 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331958 | 187908 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DP | NP190DP | np19 0dp | np190dp | Newport | Casnewydd | Caerleon Road STW | 2390 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331978 | 187895 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DQ | NP190DQ | np19 0dq | np190dq | Newport | Casnewydd | Caerleon Road STW | 2291 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332051 | 187962 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DR | NP190DR | np19 0dr | np190dr | Newport | Casnewydd | Caerleon Road STW | 2376 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332017 | 187874 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DS | NP190DS | np19 0ds | np190ds | Newport | Casnewydd | Caerleon Road STW | 2348 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332083 | 187848 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DT | NP190DT | np19 0dt | np190dt | Newport | Casnewydd | Caerleon Road STW | 2347 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332164 | 187774 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DU | NP190DU | np19 0du | np190du | Newport | Casnewydd | Caerleon Road STW | 2367 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332156 | 187755 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DW | NP190DW | np19 0dw | np190dw | Newport | Casnewydd | Caerleon Road STW | 2286 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332305 | 187736 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DX | NP190DX | np19 0dx | np190dx | Newport | Casnewydd | Caerleon Road STW | 2316 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332179 | 187802 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DY | NP190DY | np19 0dy | np190dy | Newport | Casnewydd | Caerleon Road STW | 2292 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332217 | 187801 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0DZ | NP190DZ | np19 0dz | np190dz | Newport | Casnewydd | Caerleon Road STW | 2261 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332214 | 187845 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EA | NP190EA | np19 0ea | np190ea | Newport | Casnewydd | Caerleon Road STW | 2223 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332288 | 187831 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EB | NP190EB | np19 0eb | np190eb | Newport | Casnewydd | Caerleon Road STW | 2239 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332177 | 187908 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0ED | NP190ED | np19 0ed | np190ed | Newport | Casnewydd | Caerleon Road STW | 2163 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332173 | 188020 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EE | NP190EE | np19 0ee | np190ee | Newport | Casnewydd | Caerleon Road STW | 2012 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332290 | 188115 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EF | NP190EF | np19 0ef | np190ef | Newport | Casnewydd | Caerleon Road STW | 2058 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332263 | 188077 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EG | NP190EG | np19 0eg | np190eg | Newport | Casnewydd | Caerleon Road STW | 2102 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332221 | 188058 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EH | NP190EH | np19 0eh | np190eh | Newport | Casnewydd | Caerleon Road STW | 2159 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332202 | 187996 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EJ | NP190EJ | np19 0ej | np190ej | Newport | Casnewydd | Caerleon Road STW | 2146 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332226 | 187990 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EL | NP190EL | np19 0el | np190el | Newport | Casnewydd | Caerleon Road STW | 2084 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332296 | 188010 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EN | NP190EN | np19 0en | np190en | Newport | Casnewydd | Caerleon Road STW | 2171 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332269 | 187916 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EP | NP190EP | np19 0ep | np190ep | Newport | Casnewydd | Caerleon Road STW | 2051 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332340 | 188013 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EQ | NP190EQ | np19 0eq | np190eq | Newport | Casnewydd | Caerleon Road STW | 2152 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332337 | 187882 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0ER | NP190ER | np19 0er | np190er | Newport | Casnewydd | Caerleon Road STW | 2138 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332315 | 187919 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0ES | NP190ES | np19 0es | np190es | Newport | Casnewydd | Caerleon Road STW | 2220 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332352 | 187782 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0ET | NP190ET | np19 0et | np190et | Newport | Casnewydd | Caerleon Road STW | 1974 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332949 | 187713 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EU | NP190EU | np19 0eu | np190eu | Newport | Casnewydd | Caerleon Road STW | 2049 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332862 | 187670 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EX | NP190EX | np19 0ex | np190ex | Newport | Casnewydd | Caerleon Road STW | 1974 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332914 | 187729 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EY | NP190EY | np19 0ey | np190ey | Newport | Casnewydd | Caerleon Road STW | 1909 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332961 | 187779 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0EZ | NP190EZ | np19 0ez | np190ez | Newport | Casnewydd | Caerleon Road STW | 2215 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332487 | 187691 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FA | NP190FA | np19 0fa | np190fa | Newport | Casnewydd | Caerleon Road STW | 2255 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332385 | 187714 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FB | NP190FB | np19 0fb | np190fb | Newport | Casnewydd | Caerleon Road STW | 2307 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332367 | 187662 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FD | NP190FD | np19 0fd | np190fd | Newport | Casnewydd | Caerleon Road STW | 2225 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332410 | 187732 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FE | NP190FE | np19 0fe | np190fe | Newport | Casnewydd | Caerleon Road STW | 2142 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332433 | 187819 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FF | NP190FF | np19 0ff | np190ff | Newport | Casnewydd | Caerleon Road STW | 2134 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332483 | 187792 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FG | NP190FG | np19 0fg | np190fg | Newport | Casnewydd | Caerleon Road STW | 2161 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332504 | 187744 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FJ | NP190FJ | np19 0fj | np190fj | Newport | Casnewydd | Caerleon Road STW | 2221 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332535 | 187652 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FL | NP190FL | np19 0fl | np190fl | Newport | Casnewydd | Caerleon Road STW | 2188 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332599 | 187652 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FN | NP190FN | np19 0fn | np190fn | Newport | Casnewydd | Caerleon Road STW | 2275 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332590 | 187556 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FP | NP190FP | np19 0fp | np190fp | Newport | Casnewydd | Caerleon Road STW | 2194 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332653 | 187614 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FQ | NP190FQ | np19 0fq | np190fq | Newport | Casnewydd | Caerleon Road STW | 2130 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332689 | 187667 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FR | NP190FR | np19 0fr | np190fr | Newport | Casnewydd | Caerleon Road STW | 2100 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332755 | 187666 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FS | NP190FS | np19 0fs | np190fs | Newport | Casnewydd | Caerleon Road STW | 2238 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332663 | 187558 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FT | NP190FT | np19 0ft | np190ft | Newport | Casnewydd | Caerleon Road STW | 2157 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332775 | 187592 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FU | NP190FU | np19 0fu | np190fu | Newport | Casnewydd | Caerleon Road STW | 2109 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332865 | 187603 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FW | NP190FW | np19 0fw | np190fw | Newport | Casnewydd | Caerleon Road STW | 2259 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332741 | 187495 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FX | NP190FX | np19 0fx | np190fx | Newport | Casnewydd | Caerleon Road STW | 2257 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332789 | 187475 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FY | NP190FY | np19 0fy | np190fy | Newport | Casnewydd | Caerleon Road STW | 2185 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332790 | 187554 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0FZ | NP190FZ | np19 0fz | np190fz | Newport | Casnewydd | Caerleon Road STW | 2205 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332793 | 187530 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GA | NP190GA | np19 0ga | np190ga | Newport | Casnewydd | Caerleon Road STW | 2312 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332587 | 187516 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GB | NP190GB | np19 0gb | np190gb | Newport | Casnewydd | Caerleon Road STW | 2194 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332824 | 187528 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GD | NP190GD | np19 0gd | np190gd | Newport | Casnewydd | Caerleon Road STW | 1948 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333200 | 187653 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GE | NP190GE | np19 0ge | np190ge | Newport | Casnewydd | Caerleon Road STW | 1932 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333222 | 187664 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GF | NP190GF | np19 0gf | np190gf | Newport | Casnewydd | Caerleon Road STW | 1917 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333243 | 187674 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GG | NP190GG | np19 0gg | np190gg | Newport | Casnewydd | Caerleon Road STW | 2331 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332637 | 187467 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GH | NP190GH | np19 0gh | np190gh | Newport | Casnewydd | Caerleon Road STW | 2427 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332584 | 187386 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GJ | NP190GJ | np19 0gj | np190gj | Newport | Casnewydd | Caerleon Road STW | 2398 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332583 | 187420 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GN | NP190GN | np19 0gn | np190gn | Newport | Casnewydd | Caerleon Road STW | 2353 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332688 | 187416 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GP | NP190GP | np19 0gp | np190gp | Newport | Casnewydd | Caerleon Road STW | 2435 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332825 | 187266 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GQ | NP190GQ | np19 0gq | np190gq | Newport | Casnewydd | Caerleon Road STW | 2182 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332948 | 187490 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GR | NP190GR | np19 0gr | np190gr | Newport | Casnewydd | Caerleon Road STW | 2271 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332847 | 187434 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GS | NP190GS | np19 0gs | np190gs | Newport | Casnewydd | Caerleon Road STW | 2311 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332914 | 187365 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GT | NP190GT | np19 0gt | np190gt | Newport | Casnewydd | Caerleon Road STW | 2350 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332941 | 187314 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GU | NP190GU | np19 0gu | np190gu | Newport | Casnewydd | Caerleon Road STW | 2389 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332962 | 187265 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GW | NP190GW | np19 0gw | np190gw | Newport | Casnewydd | Caerleon Road STW | 2294 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333035 | 187342 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GX | NP190GX | np19 0gx | np190gx | Newport | Casnewydd | Caerleon Road STW | 2399 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332978 | 187249 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GY | NP190GY | np19 0gy | np190gy | Newport | Casnewydd | Caerleon Road STW | 2322 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333086 | 187297 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0GZ | NP190GZ | np19 0gz | np190gz | Newport | Casnewydd | Caerleon Road STW | 2273 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333156 | 187329 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HA | NP190HA | np19 0ha | np190ha | Newport | Casnewydd | Caerleon Road STW | 2291 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333211 | 187297 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HB | NP190HB | np19 0hb | np190hb | Newport | Casnewydd | Caerleon Road STW | 2436 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333002 | 187203 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HD | NP190HD | np19 0hd | np190hd | Newport | Casnewydd | Caerleon Road STW | 2362 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333111 | 187249 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HE | NP190HE | np19 0he | np190he | Newport | Casnewydd | Caerleon Road STW | 2469 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332935 | 187190 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HF | NP190HF | np19 0hf | np190hf | Newport | Casnewydd | Caerleon Road STW | 1965 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332356 | 188117 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HG | NP190HG | np19 0hg | np190hg | Newport | Casnewydd | Caerleon Road STW | 2118 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332936 | 187563 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HH | NP190HH | np19 0hh | np190hh | Newport | Casnewydd | Caerleon Road STW | 2221 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333262 | 187358 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HJ | NP190HJ | np19 0hj | np190hj | Newport | Casnewydd | Caerleon Road STW | 2083 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333284 | 187494 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HL | NP190HL | np19 0hl | np190hl | Newport | Casnewydd | Caerleon Road STW | 2249 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333226 | 187337 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HN | NP190HN | np19 0hn | np190hn | Newport | Casnewydd | Caerleon Road STW | 2049 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332984 | 187619 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HP | NP190HP | np19 0hp | np190hp | Newport | Casnewydd | Caerleon Road STW | 2108 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333034 | 187538 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HQ | NP190HQ | np19 0hq | np190hq | Newport | Casnewydd | Caerleon Road STW | 2008 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333016 | 187650 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HR | NP190HR | np19 0hr | np190hr | Newport | Casnewydd | Caerleon Road STW | 1988 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333078 | 187649 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HS | NP190HS | np19 0hs | np190hs | Newport | Casnewydd | Caerleon Road STW | 2070 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333167 | 187536 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HT | NP190HT | np19 0ht | np190ht | Newport | Casnewydd | Caerleon Road STW | 2049 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333277 | 187530 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HU | NP190HU | np19 0hu | np190hu | Newport | Casnewydd | Caerleon Road STW | 2159 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333127 | 187455 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HW | NP190HW | np19 0hw | np190hw | Newport | Casnewydd | Caerleon Road STW | 2151 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333208 | 187442 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HX | NP190HX | np19 0hx | np190hx | Newport | Casnewydd | Caerleon Road STW | 2164 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333231 | 187423 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HY | NP190HY | np19 0hy | np190hy | Newport | Casnewydd | Caerleon Road STW | 1936 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333340 | 187632 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0HZ | NP190HZ | np19 0hz | np190hz | Newport | Casnewydd | Caerleon Road STW | 1889 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333329 | 187683 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JA | NP190JA | np19 0ja | np190ja | Newport | Casnewydd | Caerleon Road STW | 1959 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333423 | 187594 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JB | NP190JB | np19 0jb | np190jb | Newport | Casnewydd | Caerleon Road STW | 2005 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333476 | 187541 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JD | NP190JD | np19 0jd | np190jd | Newport | Casnewydd | Caerleon Road STW | 2048 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333433 | 187503 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JE | NP190JE | np19 0je | np190je | Newport | Casnewydd | Caerleon Road STW | 2105 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333455 | 187442 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JF | NP190JF | np19 0jf | np190jf | Newport | Casnewydd | Caerleon Road STW | 2027 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333507 | 187515 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JG | NP190JG | np19 0jg | np190jg | Newport | Casnewydd | Caerleon Road STW | 2047 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333565 | 187490 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JH | NP190JH | np19 0jh | np190jh | Newport | Casnewydd | Caerleon Road STW | 2131 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333580 | 187404 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JJ | NP190JJ | np19 0jj | np190jj | Newport | Casnewydd | Caerleon Road STW | 2201 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333440 | 187348 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JL | NP190JL | np19 0jl | np190jl | Newport | Casnewydd | Caerleon Road STW | 2195 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333421 | 187356 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JN | NP190JN | np19 0jn | np190jn | Newport | Casnewydd | Caerleon Road STW | 2194 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333380 | 187363 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JP | NP190JP | np19 0jp | np190jp | Newport | Casnewydd | Caerleon Road STW | 2117 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333337 | 187449 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JQ | NP190JQ | np19 0jq | np190jq | Newport | Casnewydd | Caerleon Road STW | 2227 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333296 | 187345 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JR | NP190JR | np19 0jr | np190jr | Newport | Casnewydd | Caerleon Road STW | 2069 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333355 | 187494 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JS | NP190JS | np19 0js | np190js | Newport | Casnewydd | Caerleon Road STW | 1964 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333523 | 187577 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JT | NP190JT | np19 0jt | np190jt | Newport | Casnewydd | Caerleon Road STW | 1918 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333513 | 187624 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JU | NP190JU | np19 0ju | np190ju | Newport | Casnewydd | Caerleon Road STW | 1869 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333417 | 187686 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JW | NP190JW | np19 0jw | np190jw | Newport | Casnewydd | Caerleon Road STW | 1940 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333397 | 187618 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JX | NP190JX | np19 0jx | np190jx | Newport | Casnewydd | Caerleon Road STW | 2187 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333529 | 187352 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JY | NP190JY | np19 0jy | np190jy | Newport | Casnewydd | Caerleon Road STW | 2199 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333491 | 187344 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0JZ | NP190JZ | np19 0jz | np190jz | Newport | Casnewydd | Caerleon Road STW | 2101 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333491 | 187442 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LA | NP190LA | np19 0la | np190la | Newport | Casnewydd | Caerleon Road STW | 2492 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332304 | 187480 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LB | NP190LB | np19 0lb | np190lb | Newport | Casnewydd | Caerleon Road STW | 2536 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332227 | 187481 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LD | NP190LD | np19 0ld | np190ld | Newport | Casnewydd | Caerleon Road STW | 2566 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332268 | 187415 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LE | NP190LE | np19 0le | np190le | Newport | Casnewydd | Caerleon Road STW | 2587 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332317 | 187358 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LF | NP190LF | np19 0lf | np190lf | Newport | Casnewydd | Caerleon Road STW | 2494 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332392 | 187420 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LG | NP190LG | np19 0lg | np190lg | Newport | Casnewydd | Caerleon Road STW | 2559 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332380 | 187351 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LH | NP190LH | np19 0lh | np190lh | Newport | Casnewydd | Caerleon Road STW | 2548 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332451 | 187321 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LJ | NP190LJ | np19 0lj | np190lj | Newport | Casnewydd | Caerleon Road STW | 2509 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332425 | 187382 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LL | NP190LL | np19 0ll | np190ll | Newport | Casnewydd | Caerleon Road STW | 2512 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332504 | 187333 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LN | NP190LN | np19 0ln | np190ln | Newport | Casnewydd | Caerleon Road STW | 2619 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332231 | 187377 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LP | NP190LP | np19 0lp | np190lp | Newport | Casnewydd | Caerleon Road STW | 2608 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332371 | 187299 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LQ | NP190LQ | np19 0lq | np190lq | Newport | Casnewydd | Caerleon Road STW | 2511 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332708 | 187233 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LR | NP190LR | np19 0lr | np190lr | Newport | Casnewydd | Caerleon Road STW | 2546 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332764 | 187171 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LS | NP190LS | np19 0ls | np190ls | Newport | Casnewydd | Caerleon Road STW | 2447 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332700 | 187307 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LT | NP190LT | np19 0lt | np190lt | Newport | Casnewydd | Caerleon Road STW | 2457 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332771 | 187265 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LU | NP190LU | np19 0lu | np190lu | Newport | Casnewydd | Caerleon Road STW | 2440 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332676 | 187326 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LW | NP190LW | np19 0lw | np190lw | Newport | Casnewydd | Caerleon Road STW | 1936 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332703 | 187884 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LX | NP190LX | np19 0lx | np190lx | Newport | Casnewydd | Caerleon Road STW | 1890 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333038 | 187768 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LY | NP190LY | np19 0ly | np190ly | Newport | Casnewydd | Caerleon Road STW | 2580 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331382 | 188442 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0LZ | NP190LZ | np19 0lz | np190lz | Newport | Casnewydd | Caerleon Road STW | 2586 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331582 | 188077 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NA | NP190NA | np19 0na | np190na | Newport | Casnewydd | Caerleon Road STW | 2450 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332340 | 187507 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NB | NP190NB | np19 0nb | np190nb | Newport | Casnewydd | Caerleon Road STW | 2436 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332383 | 187495 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0ND | NP190ND | np19 0nd | np190nd | Newport | Casnewydd | Caerleon Road STW | 2426 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332420 | 187483 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NF | NP190NF | np19 0nf | np190nf | Newport | Casnewydd | Caerleon Road STW | 2410 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332658 | 187368 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NG | NP190NG | np19 0ng | np190ng | Newport | Casnewydd | Caerleon Road STW | 2416 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332463 | 187468 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NL | NP190NL | np19 0nl | np190nl | Newport | Casnewydd | Caerleon Road STW | 2553 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331709 | 187959 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NP | NP190NP | np19 0np | np190np | Newport | Casnewydd | Caerleon Road STW | 2529 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331775 | 187915 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NQ | NP190NQ | np19 0nq | np190nq | Newport | Casnewydd | Caerleon Road STW | 2514 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331819 | 187886 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NR | NP190NR | np19 0nr | np190nr | Newport | Casnewydd | Caerleon Road STW | 2503 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331858 | 187859 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NS | NP190NS | np19 0ns | np190ns | Newport | Casnewydd | Caerleon Road STW | 2578 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331591 | 188078 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NT | NP190NT | np19 0nt | np190nt | Newport | Casnewydd | Caerleon Road STW | 2556 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331592 | 188116 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NU | NP190NU | np19 0nu | np190nu | Newport | Casnewydd | Caerleon Road STW | 2565 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331616 | 188065 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NW | NP190NW | np19 0nw | np190nw | Newport | Casnewydd | Caerleon Road STW | 2532 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331649 | 188074 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NX | NP190NX | np19 0nx | np190nx | Newport | Casnewydd | Caerleon Road STW | 2577 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331605 | 188059 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NY | NP190NY | np19 0ny | np190ny | Newport | Casnewydd | Caerleon Road STW | 2594 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331592 | 188048 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0NZ | NP190NZ | np19 0nz | np190nz | Newport | Casnewydd | Caerleon Road STW | 2381 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332296 | 187623 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PA | NP190PA | np19 0pa | np190pa | Newport | Casnewydd | Caerleon Road STW | 2011 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332716 | 187788 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PB | NP190PB | np19 0pb | np190pb | Newport | Casnewydd | Caerleon Road STW | 2035 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332561 | 187858 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PD | NP190PD | np19 0pd | np190pd | Newport | Casnewydd | Caerleon Road STW | 2045 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332699 | 187759 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PE | NP190PE | np19 0pe | np190pe | Newport | Casnewydd | Caerleon Road STW | 1998 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332802 | 187756 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PF | NP190PF | np19 0pf | np190pf | Newport | Casnewydd | Caerleon Road STW | 2011 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332731 | 187780 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PG | NP190PG | np19 0pg | np190pg | Newport | Casnewydd | Caerleon Road STW | 2103 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332587 | 187759 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PH | NP190PH | np19 0ph | np190ph | Newport | Casnewydd | Caerleon Road STW | 2073 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332715 | 187718 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PJ | NP190PJ | np19 0pj | np190pj | Newport | Casnewydd | Caerleon Road STW | 2109 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332643 | 187718 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PL | NP190PL | np19 0pl | np190pl | Newport | Casnewydd | Caerleon Road STW | 1929 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332827 | 187821 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PN | NP190PN | np19 0pn | np190pn | Newport | Casnewydd | Caerleon Road STW | 2161 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332574 | 187699 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PP | NP190PP | np19 0pp | np190pp | Newport | Casnewydd | Caerleon Road STW | 2630 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331456 | 188194 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PQ | NP190PQ | np19 0pq | np190pq | Newport | Casnewydd | Caerleon Road STW | 2625 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331479 | 188164 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PR | NP190PR | np19 0pr | np190pr | Newport | Casnewydd | Caerleon Road STW | 2596 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331491 | 188202 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PS | NP190PS | np19 0ps | np190ps | Newport | Casnewydd | Caerleon Road STW | 2632 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331390 | 188308 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PT | NP190PT | np19 0pt | np190pt | Newport | Casnewydd | Caerleon Road STW | 2639 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331401 | 188272 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PU | NP190PU | np19 0pu | np190pu | Newport | Casnewydd | Caerleon Road STW | 2619 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331412 | 188294 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PW | NP190PW | np19 0pw | np190pw | Newport | Casnewydd | Caerleon Road STW | 2647 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331359 | 188336 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PX | NP190PX | np19 0px | np190px | Newport | Casnewydd | Caerleon Road STW | 2640 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331349 | 188371 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PY | NP190PY | np19 0py | np190py | Newport | Casnewydd | Caerleon Road STW | 2619 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331422 | 188275 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0PZ | NP190PZ | np19 0pz | np190pz | Newport | Casnewydd | Caerleon Road STW | 2634 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331377 | 188328 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0QA | NP190QA | np19 0qa | np190qa | Newport | Casnewydd | Caerleon Road STW | 2633 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331432 | 188229 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0QB | NP190QB | np19 0qb | np190qb | Newport | Casnewydd | Caerleon Road STW | 2608 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331453 | 188242 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0QD | NP190QD | np19 0qd | np190qd | Newport | Casnewydd | Caerleon Road STW | 2478 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331939 | 187808 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0QE | NP190QE | np19 0qe | np190qe | Newport | Casnewydd | Caerleon Road STW | 2486 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331907 | 187831 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RA | NP190RA | np19 0ra | np190ra | Newport | Casnewydd | Caerleon Road STW | 2652 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333254 | 186920 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RB | NP190RB | np19 0rb | np190rb | Newport | Casnewydd | Nash STW | 2450 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 332048 | 186118 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RD | NP190RD | np19 0rd | np190rd | Newport | Casnewydd | Nash STW | 2487 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 332129 | 186216 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RE | NP190RE | np19 0re | np190re | Newport | Casnewydd | Caerleon Road STW | 2636 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333277 | 186932 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RF | NP190RF | np19 0rf | np190rf | Newport | Casnewydd | Caerleon Road STW | 2599 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333280 | 186969 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RG | NP190RG | np19 0rg | np190rg | Newport | Casnewydd | Caerleon Road STW | 2615 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333302 | 186950 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RH | NP190RH | np19 0rh | np190rh | Newport | Casnewydd | Caerleon Road STW | 2707 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333249 | 186865 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RJ | NP190RJ | np19 0rj | np190rj | Newport | Casnewydd | Caerleon Road STW | 2237 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333465 | 187308 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RL | NP190RL | np19 0rl | np190rl | Newport | Casnewydd | Caerleon Road STW | 2533 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333436 | 187014 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RP | NP190RP | np19 0rp | np190rp | Newport | Casnewydd | Caerleon Road STW | 2494 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333366 | 187062 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RQ | NP190RQ | np19 0rq | np190rq | Newport | Casnewydd | Caerleon Road STW | 2501 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333311 | 187064 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RT | NP190RT | np19 0rt | np190rt | Newport | Casnewydd | Caerleon Road STW | 2390 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333501 | 187151 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RU | NP190RU | np19 0ru | np190ru | Newport | Casnewydd | Caerleon Road STW | 2447 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333495 | 187094 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RW | NP190RW | np19 0rw | np190rw | Newport | Casnewydd | Caerleon Road STW | 2332 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333499 | 187209 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RX | NP190RX | np19 0rx | np190rx | Newport | Casnewydd | Caerleon Road STW | 2395 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333460 | 187150 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RY | NP190RY | np19 0ry | np190ry | Newport | Casnewydd | Caerleon Road STW | 2503 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333460 | 187041 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0RZ | NP190RZ | np19 0rz | np190rz | Newport | Casnewydd | Caerleon Road STW | 2470 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333402 | 187081 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0SE | NP190SE | np19 0se | np190se | Newport | Casnewydd | Caerleon Road STW | 2226 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333538 | 187312 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0UU | NP190UU | np19 0uu | np190uu | Newport | Casnewydd | Caerleon Road STW | 2593 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331425 | 188324 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0WB | NP190WB | np19 0wb | np190wb | Newport | Casnewydd | Caerleon Road STW | 1892 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332317 | 188261 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0WF | NP190WF | np19 0wf | np190wf | Newport | Casnewydd | Caerleon Road STW | 2406 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331901 | 187957 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0XB | NP190XB | np19 0xb | np190xb | Newport | Casnewydd | Caerleon Road STW | 2565 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333086 | 187046 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 0XT | NP190XT | np19 0xt | np190xt | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 1AF | NP191AF | np19 1af | np191af | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 1BJ | NP191BJ | np19 1bj | np191bj | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 1DE | NP191DE | np19 1de | np191de | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 1DT | NP191DT | np19 1dt | np191dt | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 1EA | NP191EA | np19 1ea | np191ea | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 1EG | NP191EG | np19 1eg | np191eg | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 1EL | NP191EL | np19 1el | np191el | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 1EP | NP191EP | np19 1ep | np191ep | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 1EQ | NP191EQ | np19 1eq | np191eq | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 1ER | NP191ER | np19 1er | np191er | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AA | NP194AA | np19 4aa | np194aa | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AD | NP194AD | np19 4ad | np194ad | Newport | Casnewydd | Nash STW | 2633 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333042 | 186710 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AE | NP194AE | np19 4ae | np194ae | Newport | Casnewydd | Nash STW | 2522 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332797 | 186545 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AF | NP194AF | np19 4af | np194af | Newport | Casnewydd | Nash STW | 2639 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332935 | 186697 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AG | NP194AG | np19 4ag | np194ag | Newport | Casnewydd | Nash STW | 2650 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332785 | 186674 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AH | NP194AH | np19 4ah | np194ah | Newport | Casnewydd | Nash STW | 2607 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332754 | 186621 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AJ | NP194AJ | np19 4aj | np194aj | Newport | Casnewydd | Nash STW | 2552 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332728 | 186557 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AL | NP194AL | np19 4al | np194al | Newport | Casnewydd | Nash STW | 2693 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332812 | 186725 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AN | NP194AN | np19 4an | np194an | Newport | Casnewydd | Nash STW | 2689 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332833 | 186726 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AP | NP194AP | np19 4ap | np194ap | Newport | Casnewydd | Nash STW | 2676 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332883 | 186724 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AQ | NP194AQ | np19 4aq | np194aq | Newport | Casnewydd | Nash STW | 2657 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332854 | 186698 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AR | NP194AR | np19 4ar | np194ar | Newport | Casnewydd | Nash STW | 2721 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332665 | 186714 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AS | NP194AS | np19 4as | np194as | Newport | Casnewydd | Nash STW | 2728 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332799 | 186758 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AT | NP194AT | np19 4at | np194at | Newport | Casnewydd | Nash STW | 2750 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332759 | 186771 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AU | NP194AU | np19 4au | np194au | Newport | Casnewydd | Nash STW | 2501 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332779 | 186518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AW | NP194AW | np19 4aw | np194aw | Newport | Casnewydd | Nash STW | 2538 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332769 | 186554 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4AX | NP194AX | np19 4ax | np194ax | Newport | Casnewydd | Nash STW | 2520 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332743 | 186528 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BB | NP194BB | np19 4bb | np194bb | Newport | Casnewydd | Caerleon Road STW | 2992 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 334997 | 186825 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BD | NP194BD | np19 4bd | np194bd | Newport | Casnewydd | Nash STW | 2575 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332704 | 186574 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BE | NP194BE | np19 4be | np194be | Newport | Casnewydd | Nash STW | 2602 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332680 | 186595 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BH | NP194BH | np19 4bh | np194bh | Newport | Casnewydd | Caerleon Road STW | 2957 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 335039 | 186885 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BL | NP194BL | np19 4bl | np194bl | Newport | Casnewydd | Nash STW | 2755 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332715 | 186764 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BN | NP194BN | np19 4bn | np194bn | Newport | Casnewydd | Caerleon Road STW | 2825 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332790 | 186863 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BP | NP194BP | np19 4bp | np194bp | Newport | Casnewydd | Nash STW | 2737 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332909 | 186792 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BQ | NP194BQ | np19 4bq | np194bq | Newport | Casnewydd | Nash STW | 2700 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332715 | 186707 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BR | NP194BR | np19 4br | np194br | Newport | Casnewydd | Caerleon Road STW | 2922 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 334973 | 186891 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BT | NP194BT | np19 4bt | np194bt | Newport | Casnewydd | Caerleon Road STW | 3024 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 335006 | 186794 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BU | NP194BU | np19 4bu | np194bu | Newport | Casnewydd | Nash STW | 2889 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 334937 | 186586 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BW | NP194BW | np19 4bw | np194bw | Newport | Casnewydd | Nash STW | 2797 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332862 | 186844 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BX | NP194BX | np19 4bx | np194bx | Newport | Casnewydd | Nash STW | 2754 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332677 | 186752 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BY | NP194BY | np19 4by | np194by | Newport | Casnewydd | Nash STW | 2776 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332698 | 186781 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4BZ | NP194BZ | np19 4bz | np194bz | Newport | Casnewydd | Nash STW | 2809 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332698 | 186815 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4DA | NP194DA | np19 4da | np194da | Newport | Casnewydd | Caerleon Road STW | 2850 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332698 | 186871 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4DB | NP194DB | np19 4db | np194db | Newport | Casnewydd | Caerleon Road STW | 2837 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332729 | 186873 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4DE | NP194DE | np19 4de | np194de | Newport | Casnewydd | Nash STW | 2670 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332636 | 186652 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4DF | NP194DF | np19 4df | np194df | Newport | Casnewydd | Nash STW | 2670 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332636 | 186652 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4DL | NP194DL | np19 4dl | np194dl | Newport | Casnewydd | Caerleon Road STW | 2816 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 335007 | 187026 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4ED | NP194ED | np19 4ed | np194ed | Newport | Casnewydd | Nash STW | 2532 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333124 | 186620 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4EE | NP194EE | np19 4ee | np194ee | Newport | Casnewydd | Caerleon Road STW | 2060 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334048 | 187497 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4EF | NP194EF | np19 4ef | np194ef | Newport | Casnewydd | Caerleon Road STW | 2612 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 335020 | 187265 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4JZ | NP194JZ | np19 4jz | np194jz | Newport | Casnewydd | Caerleon Road STW | 2225 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333691 | 187306 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LA | NP194LA | np19 4la | np194la | Newport | Casnewydd | Caerleon Road STW | 2168 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333705 | 187363 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LB | NP194LB | np19 4lb | np194lb | Newport | Casnewydd | Caerleon Road STW | 2237 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333846 | 187297 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LD | NP194LD | np19 4ld | np194ld | Newport | Casnewydd | Caerleon Road STW | 2183 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333848 | 187352 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LE | NP194LE | np19 4le | np194le | Newport | Casnewydd | Caerleon Road STW | 2124 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333887 | 187413 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LF | NP194LF | np19 4lf | np194lf | Newport | Casnewydd | Caerleon Road STW | 2251 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333977 | 187295 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LG | NP194LG | np19 4lg | np194lg | Newport | Casnewydd | Caerleon Road STW | 2192 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333982 | 187354 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LH | NP194LH | np19 4lh | np194lh | Newport | Casnewydd | Caerleon Road STW | 2085 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334020 | 187467 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LJ | NP194LJ | np19 4lj | np194lj | Newport | Casnewydd | Caerleon Road STW | 2118 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334110 | 187449 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LL | NP194LL | np19 4ll | np194ll | Newport | Casnewydd | Caerleon Road STW | 2133 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334069 | 187426 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LN | NP194LN | np19 4ln | np194ln | Newport | Casnewydd | Caerleon Road STW | 2058 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334203 | 187530 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LP | NP194LP | np19 4lp | np194lp | Newport | Casnewydd | Caerleon Road STW | 2278 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334041 | 187276 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LQ | NP194LQ | np19 4lq | np194lq | Newport | Casnewydd | Caerleon Road STW | 2414 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334105 | 187148 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LR | NP194LR | np19 4lr | np194lr | Newport | Casnewydd | Caerleon Road STW | 2202 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334125 | 187366 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LS | NP194LS | np19 4ls | np194ls | Newport | Casnewydd | Caerleon Road STW | 2179 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334208 | 187407 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LT | NP194LT | np19 4lt | np194lt | Newport | Casnewydd | Caerleon Road STW | 1998 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334079 | 187565 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LU | NP194LU | np19 4lu | np194lu | Newport | Casnewydd | Caerleon Road STW | 1980 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333875 | 187557 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LW | NP194LW | np19 4lw | np194lw | Newport | Casnewydd | Caerleon Road STW | 2027 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334054 | 187531 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LX | NP194LX | np19 4lx | np194lx | Newport | Casnewydd | Caerleon Road STW | 2057 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333894 | 187481 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LY | NP194LY | np19 4ly | np194ly | Newport | Casnewydd | Caerleon Road STW | 2096 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333749 | 187435 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4LZ | NP194LZ | np19 4lz | np194lz | Newport | Casnewydd | Caerleon Road STW | 2158 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333805 | 187374 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NA | NP194NA | np19 4na | np194na | Newport | Casnewydd | Caerleon Road STW | 2164 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334272 | 187438 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NB | NP194NB | np19 4nb | np194nb | Newport | Casnewydd | Caerleon Road STW | 2170 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334417 | 187476 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4ND | NP194ND | np19 4nd | np194nd | Newport | Casnewydd | Caerleon Road STW | 2231 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 334507 | 187443 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NE | NP194NE | np19 4ne | np194ne | Newport | Casnewydd | Caerleon Road STW | 2241 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 334600 | 187470 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NF | NP194NF | np19 4nf | np194nf | Newport | Casnewydd | Caerleon Road STW | 2119 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333928 | 187422 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NG | NP194NG | np19 4ng | np194ng | Newport | Casnewydd | Caerleon Road STW | 2441 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333795 | 187091 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NH | NP194NH | np19 4nh | np194nh | Newport | Casnewydd | Caerleon Road STW | 2457 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333833 | 187076 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NJ | NP194NJ | np19 4nj | np194nj | Newport | Casnewydd | Caerleon Road STW | 2651 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333916 | 186887 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NL | NP194NL | np19 4nl | np194nl | Newport | Casnewydd | Caerleon Road STW | 2351 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333935 | 187190 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NN | NP194NN | np19 4nn | np194nn | Newport | Casnewydd | Caerleon Road STW | 2304 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333899 | 187234 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NP | NP194NP | np19 4np | np194np | Newport | Casnewydd | Caerleon Road STW | 2548 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334005 | 186999 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NQ | NP194NQ | np19 4nq | np194nq | Newport | Casnewydd | Caerleon Road STW | 2668 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333998 | 186877 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NR | NP194NR | np19 4nr | np194nr | Newport | Casnewydd | Caerleon Road STW | 2651 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334040 | 186899 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NS | NP194NS | np19 4ns | np194ns | Newport | Casnewydd | Caerleon Road STW | 2429 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333964 | 187114 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NT | NP194NT | np19 4nt | np194nt | Newport | Casnewydd | Caerleon Road STW | 2522 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333958 | 187020 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NU | NP194NU | np19 4nu | np194nu | Newport | Casnewydd | Caerleon Road STW | 2400 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333964 | 187143 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NW | NP194NW | np19 4nw | np194nw | Newport | Casnewydd | Caerleon Road STW | 2497 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334243 | 187089 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NX | NP194NX | np19 4nx | np194nx | Newport | Casnewydd | Caerleon Road STW | 2410 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334183 | 187166 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NY | NP194NY | np19 4ny | np194ny | Newport | Casnewydd | Caerleon Road STW | 2372 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334244 | 187217 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4NZ | NP194NZ | np19 4nz | np194nz | Newport | Casnewydd | Caerleon Road STW | 2524 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334299 | 187074 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PA | NP194PA | np19 4pa | np194pa | Newport | Casnewydd | Caerleon Road STW | 2575 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334401 | 187048 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PB | NP194PB | np19 4pb | np194pb | Newport | Casnewydd | Caerleon Road STW | 2531 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334461 | 187111 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PD | NP194PD | np19 4pd | np194pd | Newport | Casnewydd | Caerleon Road STW | 2343 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334366 | 187279 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PE | NP194PE | np19 4pe | np194pe | Newport | Casnewydd | Caerleon Road STW | 2427 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334488 | 187229 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PF | NP194PF | np19 4pf | np194pf | Newport | Casnewydd | Caerleon Road STW | 2368 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 334517 | 187301 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PG | NP194PG | np19 4pg | np194pg | Newport | Casnewydd | Caerleon Road STW | 2362 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 334584 | 187333 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PJ | NP194PJ | np19 4pj | np194pj | Newport | Casnewydd | Caerleon Road STW | 2713 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333871 | 186822 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PL | NP194PL | np19 4pl | np194pl | Newport | Casnewydd | Nash STW | 2152 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 332213 | 185870 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PN | NP194PN | np19 4pn | np194pn | Newport | Casnewydd | Nash STW | 2016 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 332356 | 185802 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PP | NP194PP | np19 4pp | np194pp | Newport | Casnewydd | Nash STW | 1960 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 332442 | 185790 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PQ | NP194PQ | np19 4pq | np194pq | Newport | Casnewydd | Nash STW | 2098 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 332450 | 185953 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PT | NP194PT | np19 4pt | np194pt | Newport | Casnewydd | Nash STW | 2339 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 333345 | 186446 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PU | NP194PU | np19 4pu | np194pu | Newport | Casnewydd | Nash STW | 2295 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 333116 | 186380 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PW | NP194PW | np19 4pw | np194pw | Newport | Casnewydd | Nash STW | 1759 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 333164 | 185845 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4PY | NP194PY | np19 4py | np194py | Newport | Casnewydd | Caerleon Road STW | 2277 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334138 | 187293 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QA | NP194QA | np19 4qa | np194qa | Newport | Casnewydd | Caerleon Road STW | 2696 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333839 | 186838 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QB | NP194QB | np19 4qb | np194qb | Newport | Casnewydd | Caerleon Road STW | 2647 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333771 | 186884 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QD | NP194QD | np19 4qd | np194qd | Newport | Casnewydd | Nash STW | 2665 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333788 | 186753 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QE | NP194QE | np19 4qe | np194qe | Newport | Casnewydd | Nash STW | 2693 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333749 | 186785 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QF | NP194QF | np19 4qf | np194qf | Newport | Casnewydd | Caerleon Road STW | 2711 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333609 | 186822 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QG | NP194QG | np19 4qg | np194qg | Newport | Casnewydd | Caerleon Road STW | 2703 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333444 | 186842 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QH | NP194QH | np19 4qh | np194qh | Newport | Casnewydd | Nash STW | 2671 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 333494 | 186780 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QJ | NP194QJ | np19 4qj | np194qj | Newport | Casnewydd | Caerleon Road STW | 2639 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333586 | 186895 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QL | NP194QL | np19 4ql | np194ql | Newport | Casnewydd | Caerleon Road STW | 2519 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333752 | 187012 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QN | NP194QN | np19 4qn | np194qn | Newport | Casnewydd | Caerleon Road STW | 2597 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333741 | 186934 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QP | NP194QP | np19 4qp | np194qp | Newport | Casnewydd | Caerleon Road STW | 2678 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333711 | 186853 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QQ | NP194QQ | np19 4qq | np194qq | Newport | Casnewydd | Caerleon Road STW | 2763 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 334675 | 186938 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QR | NP194QR | np19 4qr | np194qr | Newport | Casnewydd | Nash STW | 2858 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 334735 | 186662 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QU | NP194QU | np19 4qu | np194qu | Newport | Casnewydd | Nash STW | 1932 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 334199 | 185890 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4QY | NP194QY | np19 4qy | np194qy | Newport | Casnewydd | Caerleon Road STW | 2092 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334096 | 187473 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4RA | NP194RA | np19 4ra | np194ra | Newport | Casnewydd | Nash STW | 2173 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 333611 | 186276 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4RB | NP194RB | np19 4rb | np194rb | Newport | Casnewydd | Nash STW | 2492 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333757 | 186582 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4RD | NP194RD | np19 4rd | np194rd | Newport | Casnewydd | Nash STW | 1797 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 332887 | 185816 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4RE | NP194RE | np19 4re | np194re | Newport | Casnewydd | Nash STW | 1334 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 332952 | 185347 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4RF | NP194RF | np19 4rf | np194rf | Newport | Casnewydd | Nash STW | 2369 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 332776 | 186380 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4RL | NP194RL | np19 4rl | np194rl | Newport | Casnewydd | Nash STW | 2369 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 333938 | 186427 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4RN | NP194RN | np19 4rn | np194rn | Newport | Casnewydd | Nash STW | 2717 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333928 | 186784 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4RP | NP194RP | np19 4rp | np194rp | Newport | Casnewydd | Nash STW | 2238 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 333947 | 186291 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4RQ | NP194RQ | np19 4rq | np194rq | Newport | Casnewydd | Nash STW | 2233 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 333813 | 186313 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4RR | NP194RR | np19 4rr | np194rr | Newport | Casnewydd | Nash STW | 2237 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 333777 | 186322 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4RS | NP194RS | np19 4rs | np194rs | Newport | Casnewydd | Nash STW | 2644 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333522 | 186752 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4SA | NP194SA | np19 4sa | np194sa | Newport | Casnewydd | Caerleon Road STW | 1961 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333627 | 187572 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4SB | NP194SB | np19 4sb | np194sb | Newport | Casnewydd | Caerleon Road STW | 2010 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333748 | 187521 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4SD | NP194SD | np19 4sd | np194sd | Newport | Casnewydd | Caerleon Road STW | 2035 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 333655 | 187497 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4SF | NP194SF | np19 4sf | np194sf | Newport | Casnewydd | Caerleon Road STW | 1942 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333758 | 187589 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4SG | NP194SG | np19 4sg | np194sg | Newport | Casnewydd | Caerleon Road STW | 1948 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333728 | 187583 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4SJ | NP194SJ | np19 4sj | np194sj | Newport | Casnewydd | Nash STW | 2491 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 334486 | 186374 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4SL | NP194SL | np19 4sl | np194sl | Newport | Casnewydd | Nash STW | 2406 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 334369 | 186333 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4SN | NP194SN | np19 4sn | np194sn | Newport | Casnewydd | Nash STW | 2180 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334502 | 186018 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4SP | NP194SP | np19 4sp | np194sp | Newport | Casnewydd | Nash STW | 2315 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334537 | 186153 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4SQ | NP194SQ | np19 4sq | np194sq | Newport | Casnewydd | Nash STW | 2350 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334589 | 186165 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4SR | NP194SR | np19 4sr | np194sr | Newport | Casnewydd | Nash STW | 2136 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 334390 | 186027 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4ST | NP194ST | np19 4st | np194st | Newport | Casnewydd | Nash STW | 2247 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334629 | 186022 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4SU | NP194SU | np19 4su | np194su | Newport | Casnewydd | Nash STW | 1935 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 334433 | 185776 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4TA | NP194TA | np19 4ta | np194ta | Newport | Casnewydd | Caerleon Road STW | 2656 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334351 | 186951 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4TB | NP194TB | np19 4tb | np194tb | Newport | Casnewydd | Caerleon Road STW | 2642 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334179 | 186929 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4TD | NP194TD | np19 4td | np194td | Newport | Casnewydd | Caerleon Road STW | 2554 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334168 | 187017 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4TE | NP194TE | np19 4te | np194te | Newport | Casnewydd | Nash STW | 2399 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 333860 | 186473 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4TF | NP194TF | np19 4tf | np194tf | Newport | Casnewydd | Nash STW | 2653 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334072 | 186688 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4TG | NP194TG | np19 4tg | np194tg | Newport | Casnewydd | Nash STW | 2345 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 333781 | 186431 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4TH | NP194TH | np19 4th | np194th | Newport | Casnewydd | Caerleon Road STW | 2651 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334263 | 186936 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4TS | NP194TS | np19 4ts | np194ts | Newport | Casnewydd | Nash STW | 2509 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 334079 | 186538 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4TX | NP194TX | np19 4tx | np194tx | Newport | Casnewydd | Caerleon Road STW | 2825 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 334548 | 186830 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4XB | NP194XB | np19 4xb | np194xb | Newport | Casnewydd | Nash STW | 2166 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 332764 | 186164 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4XE | NP194XE | np19 4xe | np194xe | Newport | Casnewydd | Nash STW | 687 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 333350 | 184789 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4XF | NP194XF | np19 4xf | np194xf | Newport | Casnewydd | Nash STW | 1461 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 333459 | 185570 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4XH | NP194XH | np19 4xh | np194xh | Newport | Casnewydd | Nash STW | 2219 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 332697 | 186196 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4XJ | NP194XJ | np19 4xj | np194xj | Newport | Casnewydd | Nash STW | 2063 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 332667 | 186018 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4XN | NP194XN | np19 4xn | np194xn | Newport | Casnewydd | Nash STW | 2521 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334626 | 186339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 4YH | NP194YH | np19 4yh | np194yh | Newport | Casnewydd | Nash STW | 2089 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 333107 | 186170 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AA | NP197AA | np19 7aa | np197aa | Newport | Casnewydd | Caerleon Road STW | 2602 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331343 | 188474 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AB | NP197AB | np19 7ab | np197ab | Newport | Casnewydd | Caerleon Road STW | 2507 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331429 | 188514 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AD | NP197AD | np19 7ad | np197ad | Newport | Casnewydd | Caerleon Road STW | 2327 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331527 | 188755 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AE | NP197AE | np19 7ae | np197ae | Newport | Casnewydd | Caerleon Road STW | 2512 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331383 | 188612 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AF | NP197AF | np19 7af | np197af | Newport | Casnewydd | Caerleon Road STW | 2482 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331397 | 188658 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AG | NP197AG | np19 7ag | np197ag | Newport | Casnewydd | Caerleon Road STW | 2435 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331455 | 188638 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AH | NP197AH | np19 7ah | np197ah | Newport | Casnewydd | Caerleon Road STW | 2418 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331448 | 188705 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AJ | NP197AJ | np19 7aj | np197aj | Newport | Casnewydd | Caerleon Road STW | 2364 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331478 | 188784 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AL | NP197AL | np19 7al | np197al | Newport | Casnewydd | Caerleon Road STW | 2268 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331546 | 188885 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AN | NP197AN | np19 7an | np197an | Newport | Casnewydd | Caerleon Road STW | 2395 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331480 | 188684 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AP | NP197AP | np19 7ap | np197ap | Newport | Casnewydd | Caerleon Road STW | 2367 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331521 | 188656 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AQ | NP197AQ | np19 7aq | np197aq | Newport | Casnewydd | Caerleon Road STW | 2327 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331536 | 188730 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AR | NP197AR | np19 7ar | np197ar | Newport | Casnewydd | Caerleon Road STW | 2292 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331576 | 188721 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AS | NP197AS | np19 7as | np197as | Newport | Casnewydd | Caerleon Road STW | 2294 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331547 | 188796 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AT | NP197AT | np19 7at | np197at | Newport | Casnewydd | Caerleon Road STW | 2254 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331567 | 188864 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AU | NP197AU | np19 7au | np197au | Newport | Casnewydd | Caerleon Road STW | 2227 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331614 | 188808 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AW | NP197AW | np19 7aw | np197aw | Newport | Casnewydd | Caerleon Road STW | 2156 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331657 | 188907 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AX | NP197AX | np19 7ax | np197ax | Newport | Casnewydd | Caerleon Road STW | 2143 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331659 | 188944 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AY | NP197AY | np19 7ay | np197ay | Newport | Casnewydd | Caerleon Road STW | 2073 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331727 | 188963 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7AZ | NP197AZ | np19 7az | np197az | Newport | Casnewydd | Caerleon Road STW | 2179 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331661 | 188819 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BA | NP197BA | np19 7ba | np197ba | Newport | Casnewydd | Caerleon Road STW | 2085 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331777 | 188777 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BB | NP197BB | np19 7bb | np197bb | Newport | Casnewydd | Caerleon Road STW | 2029 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331806 | 188859 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BD | NP197BD | np19 7bd | np197bd | Newport | Casnewydd | Caerleon Road STW | 1973 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331847 | 188913 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BE | NP197BE | np19 7be | np197be | Newport | Casnewydd | Caerleon Road STW | 1893 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331911 | 188975 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BG | NP197BG | np19 7bg | np197bg | Newport | Casnewydd | Caerleon Road STW | 1926 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331862 | 189024 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BH | NP197BH | np19 7bh | np197bh | Newport | Casnewydd | Caerleon Road STW | 2010 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331761 | 189085 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BJ | NP197BJ | np19 7bj | np197bj | Newport | Casnewydd | Caerleon Road STW | 1299 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332441 | 189757 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BL | NP197BL | np19 7bl | np197bl | Newport | Casnewydd | Caerleon Road STW | 1083 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332665 | 189771 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BN | NP197BN | np19 7bn | np197bn | Newport | Casnewydd | Caerleon Road STW | 1223 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332514 | 189733 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BP | NP197BP | np19 7bp | np197bp | Newport | Casnewydd | Caerleon Road STW | 1241 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332510 | 189803 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BQ | NP197BQ | np19 7bq | np197bq | Newport | Casnewydd | Caerleon Road STW | 1158 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332598 | 189814 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BR | NP197BR | np19 7br | np197br | Newport | Casnewydd | Caerleon Road STW | 1100 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332634 | 189704 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BS | NP197BS | np19 7bs | np197bs | Newport | Casnewydd | Caerleon Road STW | 1295 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332454 | 189801 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BU | NP197BU | np19 7bu | np197bu | Newport | Casnewydd | Caerleon Road STW | 2357 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331574 | 188557 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BW | NP197BW | np19 7bw | np197bw | Newport | Casnewydd | Caerleon Road STW | 2131 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331760 | 188696 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BX | NP197BX | np19 7bx | np197bx | Newport | Casnewydd | Caerleon Road STW | 2001 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331866 | 188780 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BY | NP197BY | np19 7by | np197by | Newport | Casnewydd | Caerleon Road STW | 1910 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331931 | 188862 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7BZ | NP197BZ | np19 7bz | np197bz | Newport | Casnewydd | Caerleon Road STW | 1866 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331951 | 188939 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DA | NP197DA | np19 7da | np197da | Newport | Casnewydd | Caerleon Road STW | 1812 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331987 | 189002 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DB | NP197DB | np19 7db | np197db | Newport | Casnewydd | Caerleon Road STW | 1829 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331954 | 189055 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DD | NP197DD | np19 7dd | np197dd | Newport | Casnewydd | Caerleon Road STW | 1904 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331868 | 189090 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DE | NP197DE | np19 7de | np197de | Newport | Casnewydd | Caerleon Road STW | 1864 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331884 | 189211 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DF | NP197DF | np19 7df | np197df | Newport | Casnewydd | Caerleon Road STW | 1877 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331857 | 189306 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DG | NP197DG | np19 7dg | np197dg | Newport | Casnewydd | Caerleon Road STW | 1825 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331923 | 189216 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DH | NP197DH | np19 7dh | np197dh | Newport | Casnewydd | Caerleon Road STW | 1816 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331948 | 189135 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DJ | NP197DJ | np19 7dj | np197dj | Newport | Casnewydd | Caerleon Road STW | 1808 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331952 | 189155 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DL | NP197DL | np19 7dl | np197dl | Newport | Casnewydd | Caerleon Road STW | 1805 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331924 | 189353 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DN | NP197DN | np19 7dn | np197dn | Newport | Casnewydd | Caerleon Road STW | 1659 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332072 | 189342 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DP | NP197DP | np19 7dp | np197dp | Newport | Casnewydd | Caerleon Road STW | 1720 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332009 | 189365 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DQ | NP197DQ | np19 7dq | np197dq | Newport | Casnewydd | Caerleon Road STW | 1652 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332075 | 189389 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DR | NP197DR | np19 7dr | np197dr | Newport | Casnewydd | Caerleon Road STW | 1811 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331914 | 189403 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DS | NP197DS | np19 7ds | np197ds | Newport | Casnewydd | Caerleon Road STW | 1717 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332024 | 189268 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DT | NP197DT | np19 7dt | np197dt | Newport | Casnewydd | Caerleon Road STW | 1706 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332049 | 189191 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DU | NP197DU | np19 7du | np197du | Newport | Casnewydd | Caerleon Road STW | 1761 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332011 | 189106 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DX | NP197DX | np19 7dx | np197dx | Newport | Casnewydd | Caerleon Road STW | 1684 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332058 | 189260 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DY | NP197DY | np19 7dy | np197dy | Newport | Casnewydd | Caerleon Road STW | 1783 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331956 | 189276 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7DZ | NP197DZ | np19 7dz | np197dz | Newport | Casnewydd | Caerleon Road STW | 2221 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331692 | 188626 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7ED | NP197ED | np19 7ed | np197ed | Newport | Casnewydd | Caerleon Road STW | 2224 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331638 | 188751 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EE | NP197EE | np19 7ee | np197ee | Newport | Casnewydd | Caerleon Road STW | 301 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 333514 | 189311 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EF | NP197EF | np19 7ef | np197ef | Newport | Casnewydd | Caerleon Road STW | 2078 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331667 | 189214 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EG | NP197EG | np19 7eg | np197eg | Newport | Casnewydd | Caerleon Road STW | 2105 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331806 | 188656 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EH | NP197EH | np19 7eh | np197eh | Newport | Casnewydd | Caerleon Road STW | 2094 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331831 | 188628 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EJ | NP197EJ | np19 7ej | np197ej | Newport | Casnewydd | Caerleon Road STW | 2006 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331913 | 188661 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EL | NP197EL | np19 7el | np197el | Newport | Casnewydd | Caerleon Road STW | 1882 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332027 | 188709 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EN | NP197EN | np19 7en | np197en | Newport | Casnewydd | Caerleon Road STW | 1783 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332095 | 188797 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EP | NP197EP | np19 7ep | np197ep | Newport | Casnewydd | Caerleon Road STW | 1778 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332069 | 188871 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EQ | NP197EQ | np19 7eq | np197eq | Newport | Casnewydd | Caerleon Road STW | 1778 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332045 | 188935 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7ER | NP197ER | np19 7er | np197er | Newport | Casnewydd | Caerleon Road STW | 1700 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332154 | 188870 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7ES | NP197ES | np19 7es | np197es | Newport | Casnewydd | Caerleon Road STW | 1618 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332231 | 188899 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7ET | NP197ET | np19 7et | np197et | Newport | Casnewydd | Caerleon Road STW | 1672 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332121 | 189045 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EU | NP197EU | np19 7eu | np197eu | Newport | Casnewydd | Caerleon Road STW | 1647 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332166 | 188986 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EW | NP197EW | np19 7ew | np197ew | Newport | Casnewydd | Caerleon Road STW | 1673 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332150 | 188953 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EX | NP197EX | np19 7ex | np197ex | Newport | Casnewydd | Caerleon Road STW | 1708 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332130 | 188907 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EY | NP197EY | np19 7ey | np197ey | Newport | Casnewydd | Caerleon Road STW | 1711 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332102 | 188976 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7EZ | NP197EZ | np19 7ez | np197ez | Newport | Casnewydd | Caerleon Road STW | 1824 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332035 | 188832 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FA | NP197FA | np19 7fa | np197fa | Newport | Casnewydd | Caerleon Road STW | 1988 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331890 | 188756 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FB | NP197FB | np19 7fb | np197fb | Newport | Casnewydd | Caerleon Road STW | 1839 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332038 | 188787 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FD | NP197FD | np19 7fd | np197fd | Newport | Casnewydd | Caerleon Road STW | 1843 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332007 | 188852 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FE | NP197FE | np19 7fe | np197fe | Newport | Casnewydd | Caerleon Road STW | 1904 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331963 | 188799 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FF | NP197FF | np19 7ff | np197ff | Newport | Casnewydd | Caerleon Road STW | 1926 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331953 | 188766 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FG | NP197FG | np19 7fg | np197fg | Newport | Casnewydd | Caerleon Road STW | 1969 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331918 | 188738 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FH | NP197FH | np19 7fh | np197fh | Newport | Casnewydd | Caerleon Road STW | 2009 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331882 | 188721 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FJ | NP197FJ | np19 7fj | np197fj | Newport | Casnewydd | Caerleon Road STW | 2068 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331833 | 188685 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FL | NP197FL | np19 7fl | np197fl | Newport | Casnewydd | Caerleon Road STW | 1800 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331951 | 189200 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FN | NP197FN | np19 7fn | np197fn | Newport | Casnewydd | Caerleon Road STW | 1781 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331976 | 189173 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FP | NP197FP | np19 7fp | np197fp | Newport | Casnewydd | Caerleon Road STW | 1755 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331998 | 189193 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FQ | NP197FQ | np19 7fq | np197fq | Newport | Casnewydd | Caerleon Road STW | 2002 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331727 | 189351 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FR | NP197FR | np19 7fr | np197fr | Newport | Casnewydd | Caerleon Road STW | 2026 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331700 | 189381 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FS | NP197FS | np19 7fs | np197fs | Newport | Casnewydd | Caerleon Road STW | 938 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332825 | 189250 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FT | NP197FT | np19 7ft | np197ft | Newport | Casnewydd | Caerleon Road STW | 1536 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332191 | 189389 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FU | NP197FU | np19 7fu | np197fu | Newport | Casnewydd | Caerleon Road STW | 1729 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332047 | 189096 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FW | NP197FW | np19 7fw | np197fw | Newport | Casnewydd | Caerleon Road STW | 1756 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332031 | 189053 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FX | NP197FX | np19 7fx | np197fx | Newport | Casnewydd | Caerleon Road STW | 1706 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332065 | 189119 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FY | NP197FY | np19 7fy | np197fy | Newport | Casnewydd | Caerleon Road STW | 1653 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332114 | 189142 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7FZ | NP197FZ | np19 7fz | np197fz | Newport | Casnewydd | Caerleon Road STW | 1615 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332163 | 189102 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GA | NP197GA | np19 7ga | np197ga | Newport | Casnewydd | Caerleon Road STW | 1576 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332230 | 189017 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GB | NP197GB | np19 7gb | np197gb | Newport | Casnewydd | Caerleon Road STW | 1548 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332297 | 188922 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GD | NP197GD | np19 7gd | np197gd | Newport | Casnewydd | Caerleon Road STW | 1494 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332350 | 188935 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GE | NP197GE | np19 7ge | np197ge | Newport | Casnewydd | Caerleon Road STW | 1472 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332337 | 189028 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GF | NP197GF | np19 7gf | np197gf | Newport | Casnewydd | Caerleon Road STW | 1384 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332394 | 189136 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GG | NP197GG | np19 7gg | np197gg | Newport | Casnewydd | Caerleon Road STW | 1562 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332203 | 189162 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GH | NP197GH | np19 7gh | np197gh | Newport | Casnewydd | Caerleon Road STW | 1514 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332272 | 189088 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GJ | NP197GJ | np19 7gj | np197gj | Newport | Casnewydd | Caerleon Road STW | 1475 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332271 | 189255 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GL | NP197GL | np19 7gl | np197gl | Newport | Casnewydd | Caerleon Road STW | 1451 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332318 | 189158 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GN | NP197GN | np19 7gn | np197gn | Newport | Casnewydd | Caerleon Road STW | 1361 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332404 | 189184 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GP | NP197GP | np19 7gp | np197gp | Newport | Casnewydd | Caerleon Road STW | 1324 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332421 | 189278 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GQ | NP197GQ | np19 7gq | np197gq | Newport | Casnewydd | Caerleon Road STW | 1575 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332152 | 189384 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GR | NP197GR | np19 7gr | np197gr | Newport | Casnewydd | Caerleon Road STW | 1563 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332158 | 189503 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GS | NP197GS | np19 7gs | np197gs | Newport | Casnewydd | Caerleon Road STW | 1738 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332055 | 189034 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7GZ | NP197GZ | np19 7gz | np197gz | Newport | Casnewydd | Caerleon Road STW | 1832 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331988 | 188935 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HA | NP197HA | np19 7ha | np197ha | Newport | Casnewydd | Caerleon Road STW | 1624 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332117 | 189273 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HB | NP197HB | np19 7hb | np197hb | Newport | Casnewydd | Caerleon Road STW | 1592 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332129 | 189475 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HD | NP197HD | np19 7hd | np197hd | Newport | Casnewydd | Caerleon Road STW | 1565 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332159 | 189641 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HE | NP197HE | np19 7he | np197he | Newport | Casnewydd | Caerleon Road STW | 1535 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332189 | 189637 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HF | NP197HF | np19 7hf | np197hf | Newport | Casnewydd | Caerleon Road STW | 1678 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332051 | 189701 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HG | NP197HG | np19 7hg | np197hg | Newport | Casnewydd | Caerleon Road STW | 1799 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 331948 | 189839 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HH | NP197HH | np19 7hh | np197hh | Newport | Casnewydd | Caerleon Road STW | 1676 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332119 | 190023 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HJ | NP197HJ | np19 7hj | np197hj | Newport | Casnewydd | Caerleon Road STW | 1815 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 331910 | 189654 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HL | NP197HL | np19 7hl | np197hl | Newport | Casnewydd | Caerleon Road STW | 1841 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 331880 | 189573 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HN | NP197HN | np19 7hn | np197hn | Newport | Casnewydd | Caerleon Road STW | 1801 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331920 | 189496 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HP | NP197HP | np19 7hp | np197hp | Newport | Casnewydd | Caerleon Road STW | 1852 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 331869 | 189515 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HQ | NP197HQ | np19 7hq | np197hq | Newport | Casnewydd | Caerleon Road STW | 1864 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331858 | 189467 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HR | NP197HR | np19 7hr | np197hr | Newport | Casnewydd | Caerleon Road STW | 1763 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331958 | 189498 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HS | NP197HS | np19 7hs | np197hs | Newport | Casnewydd | Caerleon Road STW | 1754 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 331970 | 189644 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HT | NP197HT | np19 7ht | np197ht | Newport | Casnewydd | Caerleon Road STW | 1693 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332030 | 189628 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HU | NP197HU | np19 7hu | np197hu | Newport | Casnewydd | Caerleon Road STW | 1702 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332019 | 189492 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HW | NP197HW | np19 7hw | np197hw | Newport | Casnewydd | Caerleon Road STW | 1634 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332087 | 189556 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HX | NP197HX | np19 7hx | np197hx | Newport | Casnewydd | Caerleon Road STW | 1397 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332356 | 189829 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HY | NP197HY | np19 7hy | np197hy | Newport | Casnewydd | Caerleon Road STW | 1471 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332321 | 189983 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7HZ | NP197HZ | np19 7hz | np197hz | Newport | Casnewydd | Caerleon Road STW | 1449 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332315 | 189881 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JA | NP197JA | np19 7ja | np197ja | Newport | Casnewydd | Caerleon Road STW | 1539 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332239 | 189945 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JB | NP197JB | np19 7jb | np197jb | Newport | Casnewydd | Caerleon Road STW | 1304 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332485 | 189948 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JD | NP197JD | np19 7jd | np197jd | Newport | Casnewydd | Caerleon Road STW | 1121 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332678 | 189941 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JE | NP197JE | np19 7je | np197je | Newport | Casnewydd | Caerleon Road STW | 1792 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 331933 | 189652 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JF | NP197JF | np19 7jf | np197jf | Newport | Casnewydd | Caerleon Road STW | 1740 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331981 | 189491 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JG | NP197JG | np19 7jg | np197jg | Newport | Casnewydd | Caerleon Road STW | 1679 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332042 | 189487 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JH | NP197JH | np19 7jh | np197jh | Newport | Casnewydd | Caerleon Road STW | 1734 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332018 | 189856 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JJ | NP197JJ | np19 7jj | np197jj | Newport | Casnewydd | Caerleon Road STW | 1701 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332039 | 189787 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JL | NP197JL | np19 7jl | np197jl | Newport | Casnewydd | Caerleon Road STW | 938 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332887 | 189961 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JN | NP197JN | np19 7jn | np197jn | Newport | Casnewydd | Caerleon Road STW | 1493 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332280 | 189922 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JP | NP197JP | np19 7jp | np197jp | Newport | Casnewydd | Caerleon Road STW | 1378 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332413 | 189965 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JQ | NP197JQ | np19 7jq | np197jq | Newport | Casnewydd | Caerleon Road STW | 1635 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332100 | 189745 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JR | NP197JR | np19 7jr | np197jr | Newport | Casnewydd | Caerleon Road STW | 1745 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 331991 | 189758 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JS | NP197JS | np19 7js | np197js | Newport | Casnewydd | Caerleon Road STW | 1385 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332380 | 189877 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JT | NP197JT | np19 7jt | np197jt | Newport | Casnewydd | Caerleon Road STW | 1511 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332217 | 189376 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JU | NP197JU | np19 7ju | np197ju | Newport | Casnewydd | Caerleon Road STW | 1490 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332242 | 189349 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JW | NP197JW | np19 7jw | np197jw | Newport | Casnewydd | Caerleon Road STW | 1524 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332198 | 189475 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JX | NP197JX | np19 7jx | np197jx | Newport | Casnewydd | Caerleon Road STW | 1450 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332275 | 189640 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JY | NP197JY | np19 7jy | np197jy | Newport | Casnewydd | Caerleon Road STW | 1377 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332345 | 189599 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7JZ | NP197JZ | np19 7jz | np197jz | Newport | Casnewydd | Caerleon Road STW | 1463 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332258 | 189557 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LA | NP197LA | np19 7la | np197la | Newport | Casnewydd | Caerleon Road STW | 1410 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332319 | 189379 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LB | NP197LB | np19 7lb | np197lb | Newport | Casnewydd | Caerleon Road STW | 1235 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332493 | 189391 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LD | NP197LD | np19 7ld | np197ld | Newport | Casnewydd | Caerleon Road STW | 1101 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332630 | 189379 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LE | NP197LE | np19 7le | np197le | Newport | Casnewydd | Caerleon Road STW | 1077 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332667 | 189305 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LF | NP197LF | np19 7lf | np197lf | Newport | Casnewydd | Caerleon Road STW | 1138 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332611 | 189276 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LG | NP197LG | np19 7lg | np197lg | Newport | Casnewydd | Caerleon Road STW | 1036 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332735 | 189211 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LH | NP197LH | np19 7lh | np197lh | Newport | Casnewydd | Caerleon Road STW | 980 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332819 | 189146 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LJ | NP197LJ | np19 7lj | np197lj | Newport | Casnewydd | Caerleon Road STW | 1077 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332777 | 190049 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LL | NP197LL | np19 7ll | np197ll | Newport | Casnewydd | Caerleon Road STW | 1195 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332657 | 190075 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LN | NP197LN | np19 7ln | np197ln | Newport | Casnewydd | Caerleon Road STW | 1246 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332579 | 190029 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LP | NP197LP | np19 7lp | np197lp | Newport | Casnewydd | Caerleon Road STW | 1629 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332092 | 189501 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LT | NP197LT | np19 7lt | np197lt | Newport | Casnewydd | Caerleon Road STW | 1277 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332494 | 189886 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LU | NP197LU | np19 7lu | np197lu | Newport | Casnewydd | Caerleon Road STW | 1296 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332483 | 189916 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LW | NP197LW | np19 7lw | np197lw | Newport | Casnewydd | Caerleon Road STW | 1112 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332664 | 189878 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LX | NP197LX | np19 7lx | np197lx | Newport | Casnewydd | Caerleon Road STW | 1103 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332683 | 189906 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LY | NP197LY | np19 7ly | np197ly | Newport | Casnewydd | Caerleon Road STW | 742 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333055 | 189858 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7LZ | NP197LZ | np19 7lz | np197lz | Newport | Casnewydd | Caerleon Road STW | 712 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333069 | 189817 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NA | NP197NA | np19 7na | np197na | Newport | Casnewydd | Caerleon Road STW | 437 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333337 | 189740 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NB | NP197NB | np19 7nb | np197nb | Newport | Casnewydd | Caerleon Road STW | 969 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332787 | 189791 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7ND | NP197ND | np19 7nd | np197nd | Newport | Casnewydd | Caerleon Road STW | 835 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332915 | 189750 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NE | NP197NE | np19 7ne | np197ne | Newport | Casnewydd | Caerleon Road STW | 907 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332821 | 189650 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NF | NP197NF | np19 7nf | np197nf | Newport | Casnewydd | Caerleon Road STW | 648 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333082 | 189642 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NG | NP197NG | np19 7ng | np197ng | Newport | Casnewydd | Caerleon Road STW | 775 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332950 | 189613 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NH | NP197NH | np19 7nh | np197nh | Newport | Casnewydd | Caerleon Road STW | 945 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332791 | 189699 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NJ | NP197NJ | np19 7nj | np197nj | Newport | Casnewydd | Caerleon Road STW | 648 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333075 | 189591 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NL | NP197NL | np19 7nl | np197nl | Newport | Casnewydd | Caerleon Road STW | 956 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332823 | 189861 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NN | NP197NN | np19 7nn | np197nn | Newport | Casnewydd | Caerleon Road STW | 964 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332828 | 189894 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NP | NP197NP | np19 7np | np197np | Newport | Casnewydd | Caerleon Road STW | 459 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333261 | 189532 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NQ | NP197NQ | np19 7nq | np197nq | Newport | Casnewydd | Caerleon Road STW | 519 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333202 | 189555 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NR | NP197NR | np19 7nr | np197nr | Newport | Casnewydd | Caerleon Road STW | 519 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333202 | 189550 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NS | NP197NS | np19 7ns | np197ns | Newport | Casnewydd | Caerleon Road STW | 623 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333103 | 189612 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NT | NP197NT | np19 7nt | np197nt | Newport | Casnewydd | Caerleon Road STW | 561 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333161 | 189572 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NU | NP197NU | np19 7nu | np197nu | Newport | Casnewydd | Caerleon Road STW | 475 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333249 | 189589 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NW | NP197NW | np19 7nw | np197nw | Newport | Casnewydd | Caerleon Road STW | 399 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333322 | 189552 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NX | NP197NX | np19 7nx | np197nx | Newport | Casnewydd | Caerleon Road STW | 610 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333126 | 189669 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NY | NP197NY | np19 7ny | np197ny | Newport | Casnewydd | Caerleon Road STW | 684 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333077 | 189764 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7NZ | NP197NZ | np19 7nz | np197nz | Newport | Casnewydd | Caerleon Road STW | 464 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333264 | 189615 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PA | NP197PA | np19 7pa | np197pa | Newport | Casnewydd | Caerleon Road STW | 312 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333408 | 189542 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PB | NP197PB | np19 7pb | np197pb | Newport | Casnewydd | Caerleon Road STW | 297 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333455 | 189397 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PD | NP197PD | np19 7pd | np197pd | Newport | Casnewydd | Caerleon Road STW | 367 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333491 | 189243 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PE | NP197PE | np19 7pe | np197pe | Newport | Casnewydd | Caerleon Road STW | 408 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 333528 | 189170 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PF | NP197PF | np19 7pf | np197pf | Newport | Casnewydd | Caerleon Road STW | 459 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 333510 | 189122 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PG | NP197PG | np19 7pg | np197pg | Newport | Casnewydd | Caerleon Road STW | 497 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333489 | 189090 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PH | NP197PH | np19 7ph | np197ph | Newport | Casnewydd | Caerleon Road STW | 540 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333480 | 189047 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PJ | NP197PJ | np19 7pj | np197pj | Newport | Casnewydd | Caerleon Road STW | 641 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333439 | 188954 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PL | NP197PL | np19 7pl | np197pl | Newport | Casnewydd | Caerleon Road STW | 616 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333376 | 189019 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PN | NP197PN | np19 7pn | np197pn | Newport | Casnewydd | Caerleon Road STW | 544 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333364 | 189119 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PP | NP197PP | np19 7pp | np197pp | Newport | Casnewydd | Caerleon Road STW | 506 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333392 | 189145 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PQ | NP197PQ | np19 7pq | np197pq | Newport | Casnewydd | Caerleon Road STW | 473 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333408 | 189175 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PR | NP197PR | np19 7pr | np197pr | Newport | Casnewydd | Caerleon Road STW | 434 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333422 | 189215 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PS | NP197PS | np19 7ps | np197ps | Newport | Casnewydd | Caerleon Road STW | 440 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333371 | 189262 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PT | NP197PT | np19 7pt | np197pt | Newport | Casnewydd | Caerleon Road STW | 423 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333355 | 189316 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PU | NP197PU | np19 7pu | np197pu | Newport | Casnewydd | Caerleon Road STW | 471 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333316 | 189288 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PW | NP197PW | np19 7pw | np197pw | Newport | Casnewydd | Caerleon Road STW | 529 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333246 | 189296 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PX | NP197PX | np19 7px | np197px | Newport | Casnewydd | Caerleon Road STW | 623 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333100 | 189468 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PY | NP197PY | np19 7py | np197py | Newport | Casnewydd | Caerleon Road STW | 774 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332947 | 189567 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7PZ | NP197PZ | np19 7pz | np197pz | Newport | Casnewydd | Caerleon Road STW | 661 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333059 | 189536 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QA | NP197QA | np19 7qa | np197qa | Newport | Casnewydd | Caerleon Road STW | 661 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333087 | 189719 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QB | NP197QB | np19 7qb | np197qb | Newport | Casnewydd | Caerleon Road STW | 572 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333194 | 189306 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QL | NP197QL | np19 7ql | np197ql | Newport | Casnewydd | Caerleon Road STW | 762 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333378 | 188849 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QN | NP197QN | np19 7qn | np197qn | Newport | Casnewydd | Caerleon Road STW | 895 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333161 | 188832 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QP | NP197QP | np19 7qp | np197qp | Newport | Casnewydd | Caerleon Road STW | 797 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333184 | 188941 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QQ | NP197QQ | np19 7qq | np197qq | Newport | Casnewydd | Caerleon Road STW | 699 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333254 | 189009 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QR | NP197QR | np19 7qr | np197qr | Newport | Casnewydd | Caerleon Road STW | 845 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333130 | 188925 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QS | NP197QS | np19 7qs | np197qs | Newport | Casnewydd | Caerleon Road STW | 844 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333064 | 188999 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QT | NP197QT | np19 7qt | np197qt | Newport | Casnewydd | Caerleon Road STW | 780 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333074 | 189093 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QU | NP197QU | np19 7qu | np197qu | Newport | Casnewydd | Caerleon Road STW | 700 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333184 | 189080 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QW | NP197QW | np19 7qw | np197qw | Newport | Casnewydd | Caerleon Road STW | 735 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333090 | 189151 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QX | NP197QX | np19 7qx | np197qx | Newport | Casnewydd | Caerleon Road STW | 868 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332900 | 189247 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QY | NP197QY | np19 7qy | np197qy | Newport | Casnewydd | Caerleon Road STW | 841 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332913 | 189296 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7QZ | NP197QZ | np19 7qz | np197qz | Newport | Casnewydd | Caerleon Road STW | 986 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332745 | 189383 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7RA | NP197RA | np19 7ra | np197ra | Newport | Casnewydd | Caerleon Road STW | 930 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332801 | 189390 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7RB | NP197RB | np19 7rb | np197rb | Newport | Casnewydd | Caerleon Road STW | 915 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332811 | 189428 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7RD | NP197RD | np19 7rd | np197rd | Newport | Casnewydd | Caerleon Road STW | 931 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332792 | 189461 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7RE | NP197RE | np19 7re | np197re | Newport | Casnewydd | Caerleon Road STW | 807 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332930 | 189369 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7RF | NP197RF | np19 7rf | np197rf | Newport | Casnewydd | Caerleon Road STW | 705 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333088 | 189218 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7RG | NP197RG | np19 7rg | np197rg | Newport | Casnewydd | Caerleon Road STW | 699 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333063 | 189292 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7RH | NP197RH | np19 7rh | np197rh | Newport | Casnewydd | Caerleon Road STW | 955 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332784 | 189343 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7RU | NP197RU | np19 7ru | np197ru | Newport | Casnewydd | Caerleon Road STW | 1207 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332587 | 189115 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7RW | NP197RW | np19 7rw | np197rw | Newport | Casnewydd | Caerleon Road STW | 1254 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332574 | 189023 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7RX | NP197RX | np19 7rx | np197rx | Newport | Casnewydd | Caerleon Road STW | 1221 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332594 | 189058 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7RY | NP197RY | np19 7ry | np197ry | Newport | Casnewydd | Caerleon Road STW | 1088 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332812 | 188931 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7RZ | NP197RZ | np19 7rz | np197rz | Newport | Casnewydd | Caerleon Road STW | 959 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332969 | 188934 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SA | NP197SA | np19 7sa | np197sa | Newport | Casnewydd | Caerleon Road STW | 938 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333131 | 188801 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SB | NP197SB | np19 7sb | np197sb | Newport | Casnewydd | Caerleon Road STW | 1051 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332922 | 188847 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SD | NP197SD | np19 7sd | np197sd | Newport | Casnewydd | Caerleon Road STW | 1056 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332889 | 188879 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SE | NP197SE | np19 7se | np197se | Newport | Casnewydd | Caerleon Road STW | 1060 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332865 | 188904 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SF | NP197SF | np19 7sf | np197sf | Newport | Casnewydd | Caerleon Road STW | 1133 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332854 | 188800 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SG | NP197SG | np19 7sg | np197sg | Newport | Casnewydd | Caerleon Road STW | 1144 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332782 | 188875 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SH | NP197SH | np19 7sh | np197sh | Newport | Casnewydd | Caerleon Road STW | 1107 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332817 | 188891 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SJ | NP197SJ | np19 7sj | np197sj | Newport | Casnewydd | Caerleon Road STW | 1201 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332738 | 188840 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SL | NP197SL | np19 7sl | np197sl | Newport | Casnewydd | Caerleon Road STW | 1228 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332645 | 188937 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SN | NP197SN | np19 7sn | np197sn | Newport | Casnewydd | Caerleon Road STW | 1182 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332719 | 188903 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SP | NP197SP | np19 7sp | np197sp | Newport | Casnewydd | Caerleon Road STW | 1376 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332520 | 188857 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SQ | NP197SQ | np19 7sq | np197sq | Newport | Casnewydd | Caerleon Road STW | 1338 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332534 | 188912 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SR | NP197SR | np19 7sr | np197sr | Newport | Casnewydd | Caerleon Road STW | 1427 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332416 | 188951 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7SS | NP197SS | np19 7ss | np197ss | Newport | Casnewydd | Caerleon Road STW | 1371 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332426 | 189077 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7TA | NP197TA | np19 7ta | np197ta | Newport | Casnewydd | Caerleon Road STW | 909 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332896 | 189146 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7TB | NP197TB | np19 7tb | np197tb | Newport | Casnewydd | Caerleon Road STW | 881 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332959 | 189086 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7TD | NP197TD | np19 7td | np197td | Newport | Casnewydd | Caerleon Road STW | 960 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332868 | 189089 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7TE | NP197TE | np19 7te | np197te | Newport | Casnewydd | Caerleon Road STW | 922 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332921 | 189071 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7TF | NP197TF | np19 7tf | np197tf | Newport | Casnewydd | Caerleon Road STW | 904 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332966 | 189032 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7TG | NP197TG | np19 7tg | np197tg | Newport | Casnewydd | Caerleon Road STW | 916 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332961 | 189018 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7TH | NP197TH | np19 7th | np197th | Newport | Casnewydd | Caerleon Road STW | 1057 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332775 | 189057 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7TJ | NP197TJ | np19 7tj | np197tj | Newport | Casnewydd | Caerleon Road STW | 1062 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332795 | 189009 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7UB | NP197UB | np19 7ub | np197ub | Newport | Casnewydd | Caerleon Road STW | 462 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333258 | 189534 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 7XU | NP197XU | np19 7xu | np197xu | Newport | Casnewydd | Caerleon Road STW | 1292 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332430 | 189590 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AA | NP198AA | np19 8aa | np198aa | Newport | Casnewydd | Caerleon Road STW | 1258 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333300 | 188345 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AB | NP198AB | np19 8ab | np198ab | Newport | Casnewydd | Caerleon Road STW | 1256 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333389 | 188319 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AD | NP198AD | np19 8ad | np198ad | Newport | Casnewydd | Caerleon Road STW | 1180 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333435 | 188385 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AE | NP198AE | np19 8ae | np198ae | Newport | Casnewydd | Caerleon Road STW | 1117 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333487 | 188438 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AF | NP198AF | np19 8af | np198af | Newport | Casnewydd | Caerleon Road STW | 1032 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 333523 | 188517 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AG | NP198AG | np19 8ag | np198ag | Newport | Casnewydd | Caerleon Road STW | 917 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 333564 | 188627 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AH | NP198AH | np19 8ah | np198ah | Newport | Casnewydd | Caerleon Road STW | 927 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333439 | 188647 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AJ | NP198AJ | np19 8aj | np198aj | Newport | Casnewydd | Caerleon Road STW | 1000 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333256 | 188645 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AP | NP198AP | np19 8ap | np198ap | Newport | Casnewydd | Caerleon Road STW | 2112 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331893 | 188471 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AQ | NP198AQ | np19 8aq | np198aq | Newport | Casnewydd | Caerleon Road STW | 1291 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333491 | 188260 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AR | NP198AR | np19 8ar | np198ar | Newport | Casnewydd | Caerleon Road STW | 1347 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333366 | 188231 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AS | NP198AS | np19 8as | np198as | Newport | Casnewydd | Caerleon Road STW | 1381 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333387 | 188190 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AT | NP198AT | np19 8at | np198at | Newport | Casnewydd | Caerleon Road STW | 1223 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333553 | 188319 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AU | NP198AU | np19 8au | np198au | Newport | Casnewydd | Caerleon Road STW | 1068 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333649 | 188465 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AW | NP198AW | np19 8aw | np198aw | Newport | Casnewydd | Caerleon Road STW | 925 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 333700 | 188606 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AX | NP198AX | np19 8ax | np198ax | Newport | Casnewydd | Caerleon Road STW | 1133 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333696 | 188398 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AY | NP198AY | np19 8ay | np198ay | Newport | Casnewydd | Caerleon Road STW | 1329 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333577 | 188209 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8AZ | NP198AZ | np19 8az | np198az | Newport | Casnewydd | Caerleon Road STW | 1194 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333675 | 188337 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BA | NP198BA | np19 8ba | np198ba | Newport | Casnewydd | Caerleon Road STW | 1096 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333722 | 188434 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BB | NP198BB | np19 8bb | np198bb | Newport | Casnewydd | Caerleon Road STW | 958 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 333771 | 188574 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BD | NP198BD | np19 8bd | np198bd | Newport | Casnewydd | Caerleon Road STW | 871 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 333634 | 188664 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BE | NP198BE | np19 8be | np198be | Newport | Casnewydd | Caerleon Road STW | 832 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 333649 | 188701 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BG | NP198BG | np19 8bg | np198bg | Newport | Casnewydd | Caerleon Road STW | 785 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 333938 | 188776 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BH | NP198BH | np19 8bh | np198bh | Newport | Casnewydd | Caerleon Road STW | 819 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334165 | 188843 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BJ | NP198BJ | np19 8bj | np198bj | Newport | Casnewydd | Caerleon Road STW | 846 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 333960 | 188719 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BL | NP198BL | np19 8bl | np198bl | Newport | Casnewydd | Caerleon Road STW | 1014 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 333880 | 188529 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BN | NP198BN | np19 8bn | np198bn | Newport | Casnewydd | Caerleon Road STW | 1043 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333824 | 188493 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BP | NP198BP | np19 8bp | np198bp | Newport | Casnewydd | Caerleon Road STW | 1956 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332104 | 188429 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BU | NP198BU | np19 8bu | np198bu | Newport | Casnewydd | Caerleon Road STW | 1737 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332207 | 188677 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BW | NP198BW | np19 8bw | np198bw | Newport | Casnewydd | Caerleon Road STW | 2274 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331689 | 188509 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BX | NP198BX | np19 8bx | np198bx | Newport | Casnewydd | Caerleon Road STW | 2228 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331753 | 188485 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BY | NP198BY | np19 8by | np198by | Newport | Casnewydd | Caerleon Road STW | 2030 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332021 | 188420 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8BZ | NP198BZ | np19 8bz | np198bz | Newport | Casnewydd | Caerleon Road STW | 1886 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332231 | 188374 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DA | NP198DA | np19 8da | np198da | Newport | Casnewydd | Caerleon Road STW | 1889 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332169 | 188453 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DB | NP198DB | np19 8db | np198db | Newport | Casnewydd | Caerleon Road STW | 1894 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332123 | 188513 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DD | NP198DD | np19 8dd | np198dd | Newport | Casnewydd | Caerleon Road STW | 1855 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332134 | 188570 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DE | NP198DE | np19 8de | np198de | Newport | Casnewydd | Caerleon Road STW | 1955 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332061 | 188497 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DG | NP198DG | np19 8dg | np198dg | Newport | Casnewydd | Caerleon Road STW | 1892 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332099 | 188556 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DH | NP198DH | np19 8dh | np198dh | Newport | Casnewydd | Caerleon Road STW | 1947 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332035 | 188555 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DJ | NP198DJ | np19 8dj | np198dj | Newport | Casnewydd | Caerleon Road STW | 1991 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331971 | 188581 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DL | NP198DL | np19 8dl | np198dl | Newport | Casnewydd | Caerleon Road STW | 1901 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332031 | 188658 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DN | NP198DN | np19 8dn | np198dn | Newport | Casnewydd | Caerleon Road STW | 2023 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331926 | 188597 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DP | NP198DP | np19 8dp | np198dp | Newport | Casnewydd | Caerleon Road STW | 2078 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331873 | 188580 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DQ | NP198DQ | np19 8dq | np198dq | Newport | Casnewydd | Caerleon Road STW | 2122 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331814 | 188600 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DR | NP198DR | np19 8dr | np198dr | Newport | Casnewydd | Caerleon Road STW | 2155 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331798 | 188557 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DS | NP198DS | np19 8ds | np198ds | Newport | Casnewydd | Caerleon Road STW | 2092 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331883 | 188531 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DT | NP198DT | np19 8dt | np198dt | Newport | Casnewydd | Caerleon Road STW | 2028 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331960 | 188524 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DU | NP198DU | np19 8du | np198du | Newport | Casnewydd | Caerleon Road STW | 1987 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331962 | 188606 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DW | NP198DW | np19 8dw | np198dw | Newport | Casnewydd | Caerleon Road STW | 1919 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332072 | 188549 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DY | NP198DY | np19 8dy | np198dy | Newport | Casnewydd | Caerleon Road STW | 1722 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332582 | 188238 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8DZ | NP198DZ | np19 8dz | np198dz | Newport | Casnewydd | Caerleon Road STW | 1760 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332603 | 188171 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EA | NP198EA | np19 8ea | np198ea | Newport | Casnewydd | Caerleon Road STW | 2355 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331620 | 188466 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EB | NP198EB | np19 8eb | np198eb | Newport | Casnewydd | Caerleon Road STW | 2221 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331793 | 188427 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8ED | NP198ED | np19 8ed | np198ed | Newport | Casnewydd | Caerleon Road STW | 2075 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331980 | 188401 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EE | NP198EE | np19 8ee | np198ee | Newport | Casnewydd | Caerleon Road STW | 1982 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332113 | 188371 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EF | NP198EF | np19 8ef | np198ef | Newport | Casnewydd | Caerleon Road STW | 1926 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332196 | 188353 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EG | NP198EG | np19 8eg | np198eg | Newport | Casnewydd | Caerleon Road STW | 1858 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332301 | 188331 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EH | NP198EH | np19 8eh | np198eh | Newport | Casnewydd | Caerleon Road STW | 1928 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332218 | 188323 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EJ | NP198EJ | np19 8ej | np198ej | Newport | Casnewydd | Caerleon Road STW | 1818 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332408 | 188272 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EL | NP198EL | np19 8el | np198el | Newport | Casnewydd | Caerleon Road STW | 1767 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332470 | 188282 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EN | NP198EN | np19 8en | np198en | Newport | Casnewydd | Caerleon Road STW | 1711 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332569 | 188265 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EP | NP198EP | np19 8ep | np198ep | Newport | Casnewydd | Caerleon Road STW | 1764 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332549 | 188211 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EQ | NP198EQ | np19 8eq | np198eq | Newport | Casnewydd | Caerleon Road STW | 1850 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332506 | 188135 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8ER | NP198ER | np19 8er | np198er | Newport | Casnewydd | Caerleon Road STW | 1895 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332384 | 188187 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8ES | NP198ES | np19 8es | np198es | Newport | Casnewydd | Caerleon Road STW | 1803 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332495 | 188208 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8ET | NP198ET | np19 8et | np198et | Newport | Casnewydd | Caerleon Road STW | 1854 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332368 | 188263 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EU | NP198EU | np19 8eu | np198eu | Newport | Casnewydd | Caerleon Road STW | 1956 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332228 | 188266 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EW | NP198EW | np19 8ew | np198ew | Newport | Casnewydd | Caerleon Road STW | 1963 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332171 | 188326 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EX | NP198EX | np19 8ex | np198ex | Newport | Casnewydd | Caerleon Road STW | 1995 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332158 | 188290 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EY | NP198EY | np19 8ey | np198ey | Newport | Casnewydd | Caerleon Road STW | 2034 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332068 | 188345 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8EZ | NP198EZ | np19 8ez | np198ez | Newport | Casnewydd | Caerleon Road STW | 1609 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332346 | 188694 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FB | NP198FB | np19 8fb | np198fb | Newport | Casnewydd | Caerleon Road STW | 1705 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332370 | 188490 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FD | NP198FD | np19 8fd | np198fd | Newport | Casnewydd | Caerleon Road STW | 1699 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332404 | 188457 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FE | NP198FE | np19 8fe | np198fe | Newport | Casnewydd | Caerleon Road STW | 1683 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332467 | 188407 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FF | NP198FF | np19 8ff | np198ff | Newport | Casnewydd | Caerleon Road STW | 1768 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332323 | 188447 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FG | NP198FG | np19 8fg | np198fg | Newport | Casnewydd | Caerleon Road STW | 1826 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332242 | 188458 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FH | NP198FH | np19 8fh | np198fh | Newport | Casnewydd | Caerleon Road STW | 1838 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332197 | 188502 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FJ | NP198FJ | np19 8fj | np198fj | Newport | Casnewydd | Caerleon Road STW | 1770 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332242 | 188558 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FL | NP198FL | np19 8fl | np198fl | Newport | Casnewydd | Caerleon Road STW | 1811 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332132 | 188661 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FN | NP198FN | np19 8fn | np198fn | Newport | Casnewydd | Caerleon Road STW | 1705 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332189 | 188782 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FP | NP198FP | np19 8fp | np198fp | Newport | Casnewydd | Caerleon Road STW | 1592 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332334 | 188748 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FQ | NP198FQ | np19 8fq | np198fq | Newport | Casnewydd | Caerleon Road STW | 1475 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332517 | 188678 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FR | NP198FR | np19 8fr | np198fr | Newport | Casnewydd | Caerleon Road STW | 1618 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332365 | 188647 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FS | NP198FS | np19 8fs | np198fs | Newport | Casnewydd | Caerleon Road STW | 1660 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332358 | 188582 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FT | NP198FT | np19 8ft | np198ft | Newport | Casnewydd | Caerleon Road STW | 1590 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332417 | 188619 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FU | NP198FU | np19 8fu | np198fu | Newport | Casnewydd | Caerleon Road STW | 1675 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332398 | 188502 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FW | NP198FW | np19 8fw | np198fw | Newport | Casnewydd | Caerleon Road STW | 1746 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332189 | 188691 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FX | NP198FX | np19 8fx | np198fx | Newport | Casnewydd | Caerleon Road STW | 1706 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332228 | 188704 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FY | NP198FY | np19 8fy | np198fy | Newport | Casnewydd | Caerleon Road STW | 1600 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332422 | 188595 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8FZ | NP198FZ | np19 8fz | np198fz | Newport | Casnewydd | Caerleon Road STW | 1657 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332346 | 188605 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GA | NP198GA | np19 8ga | np198ga | Newport | Casnewydd | Caerleon Road STW | 1808 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332221 | 188521 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GB | NP198GB | np19 8gb | np198gb | Newport | Casnewydd | Caerleon Road STW | 2049 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 331932 | 188530 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GD | NP198GD | np19 8gd | np198gd | Newport | Casnewydd | Caerleon Road STW | 1462 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332680 | 188503 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GE | NP198GE | np19 8ge | np198ge | Newport | Casnewydd | Caerleon Road STW | 1812 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332347 | 188348 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GF | NP198GF | np19 8gf | np198gf | Newport | Casnewydd | Caerleon Road STW | 1704 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332423 | 188426 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GG | NP198GG | np19 8gg | np198gg | Newport | Casnewydd | Caerleon Road STW | 1551 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332498 | 188576 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GH | NP198GH | np19 8gh | np198gh | Newport | Casnewydd | Caerleon Road STW | 1763 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332420 | 188340 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GJ | NP198GJ | np19 8gj | np198gj | Newport | Casnewydd | Caerleon Road STW | 1660 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332561 | 188343 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GL | NP198GL | np19 8gl | np198gl | Newport | Casnewydd | Caerleon Road STW | 1644 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332531 | 188396 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GN | NP198GN | np19 8gn | np198gn | Newport | Casnewydd | Caerleon Road STW | 1510 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332571 | 188551 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GP | NP198GP | np19 8gp | np198gp | Newport | Casnewydd | Caerleon Road STW | 1489 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332609 | 188539 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GQ | NP198GQ | np19 8gq | np198gq | Newport | Casnewydd | Caerleon Road STW | 1500 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332684 | 188446 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GR | NP198GR | np19 8gr | np198gr | Newport | Casnewydd | Caerleon Road STW | 1534 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332693 | 188391 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GS | NP198GS | np19 8gs | np198gs | Newport | Casnewydd | Caerleon Road STW | 1461 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332809 | 188389 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GT | NP198GT | np19 8gt | np198gt | Newport | Casnewydd | Caerleon Road STW | 1373 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332809 | 188504 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GU | NP198GU | np19 8gu | np198gu | Newport | Casnewydd | Caerleon Road STW | 1580 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332740 | 188291 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GW | NP198GW | np19 8gw | np198gw | Newport | Casnewydd | Caerleon Road STW | 1551 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332814 | 188272 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GX | NP198GX | np19 8gx | np198gx | Newport | Casnewydd | Caerleon Road STW | 1621 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332743 | 188237 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8GY | NP198GY | np19 8gy | np198gy | Newport | Casnewydd | Caerleon Road STW | 1625 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332437 | 188533 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HA | NP198HA | np19 8ha | np198ha | Newport | Casnewydd | Caerleon Road STW | 1821 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332385 | 188293 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HH | NP198HH | np19 8hh | np198hh | Newport | Casnewydd | Caerleon Road STW | 1531 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333007 | 188176 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HJ | NP198HJ | np19 8hj | np198hj | Newport | Casnewydd | Caerleon Road STW | 1471 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333218 | 188148 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HL | NP198HL | np19 8hl | np198hl | Newport | Casnewydd | Caerleon Road STW | 1402 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333413 | 188163 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HN | NP198HN | np19 8hn | np198hn | Newport | Casnewydd | Caerleon Road STW | 1505 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332964 | 188229 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HP | NP198HP | np19 8hp | np198hp | Newport | Casnewydd | Caerleon Road STW | 1502 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332873 | 188290 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HQ | NP198HQ | np19 8hq | np198hq | Newport | Casnewydd | Caerleon Road STW | 1387 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332960 | 188370 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HR | NP198HR | np19 8hr | np198hr | Newport | Casnewydd | Caerleon Road STW | 1300 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333002 | 188447 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HS | NP198HS | np19 8hs | np198hs | Newport | Casnewydd | Caerleon Road STW | 1190 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333138 | 188492 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HT | NP198HT | np19 8ht | np198ht | Newport | Casnewydd | Caerleon Road STW | 1278 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333123 | 188400 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HU | NP198HU | np19 8hu | np198hu | Newport | Casnewydd | Caerleon Road STW | 1385 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333013 | 188340 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HW | NP198HW | np19 8hw | np198hw | Newport | Casnewydd | Caerleon Road STW | 1385 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333059 | 188313 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HX | NP198HX | np19 8hx | np198hx | Newport | Casnewydd | Caerleon Road STW | 1416 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333124 | 188246 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HY | NP198HY | np19 8hy | np198hy | Newport | Casnewydd | Caerleon Road STW | 1423 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333186 | 188211 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8HZ | NP198HZ | np19 8hz | np198hz | Newport | Casnewydd | Caerleon Road STW | 1450 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332911 | 188327 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JF | NP198JF | np19 8jf | np198jf | Newport | Casnewydd | Caerleon Road STW | 1424 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333472 | 188128 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JG | NP198JG | np19 8jg | np198jg | Newport | Casnewydd | Caerleon Road STW | 1457 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333336 | 188125 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JH | NP198JH | np19 8jh | np198jh | Newport | Casnewydd | Caerleon Road STW | 1516 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333195 | 188108 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JJ | NP198JJ | np19 8jj | np198jj | Newport | Casnewydd | Caerleon Road STW | 1567 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333232 | 188042 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JL | NP198JL | np19 8jl | np198jl | Newport | Casnewydd | Caerleon Road STW | 1622 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333037 | 188059 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JN | NP198JN | np19 8jn | np198jn | Newport | Casnewydd | Caerleon Road STW | 1612 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333099 | 188043 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JP | NP198JP | np19 8jp | np198jp | Newport | Casnewydd | Caerleon Road STW | 1591 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333170 | 188038 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JQ | NP198JQ | np19 8jq | np198jq | Newport | Casnewydd | Caerleon Road STW | 1545 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333294 | 188045 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JR | NP198JR | np19 8jr | np198jr | Newport | Casnewydd | Caerleon Road STW | 1624 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333268 | 187971 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JS | NP198JS | np19 8js | np198js | Newport | Casnewydd | Caerleon Road STW | 1694 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333082 | 187961 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JT | NP198JT | np19 8jt | np198jt | Newport | Casnewydd | Caerleon Road STW | 1757 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333050 | 187906 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JU | NP198JU | np19 8ju | np198ju | Newport | Casnewydd | Caerleon Road STW | 1731 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333223 | 187872 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JW | NP198JW | np19 8jw | np198jw | Newport | Casnewydd | Caerleon Road STW | 1717 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333168 | 187905 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JX | NP198JX | np19 8jx | np198jx | Newport | Casnewydd | Caerleon Road STW | 1778 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333299 | 187803 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JY | NP198JY | np19 8jy | np198jy | Newport | Casnewydd | Caerleon Road STW | 1713 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333320 | 187865 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8JZ | NP198JZ | np19 8jz | np198jz | Newport | Casnewydd | Caerleon Road STW | 1547 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333341 | 188031 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LA | NP198LA | np19 8la | np198la | Newport | Casnewydd | Caerleon Road STW | 1495 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333342 | 188084 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LB | NP198LB | np19 8lb | np198lb | Newport | Casnewydd | Caerleon Road STW | 1467 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333492 | 188081 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LD | NP198LD | np19 8ld | np198ld | Newport | Casnewydd | Caerleon Road STW | 1537 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333385 | 188030 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LE | NP198LE | np19 8le | np198le | Newport | Casnewydd | Caerleon Road STW | 1545 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333417 | 188016 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LF | NP198LF | np19 8lf | np198lf | Newport | Casnewydd | Caerleon Road STW | 1649 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333261 | 187947 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LG | NP198LG | np19 8lg | np198lg | Newport | Casnewydd | Caerleon Road STW | 1712 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333200 | 187900 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LL | NP198LL | np19 8ll | np198ll | Newport | Casnewydd | Caerleon Road STW | 1499 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332404 | 188813 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LN | NP198LN | np19 8ln | np198ln | Newport | Casnewydd | Caerleon Road STW | 1529 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332344 | 188865 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LP | NP198LP | np19 8lp | np198lp | Newport | Casnewydd | Caerleon Road STW | 1546 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 332356 | 188803 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LQ | NP198LQ | np19 8lq | np198lq | Newport | Casnewydd | Caerleon Road STW | 1404 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332516 | 188809 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LR | NP198LR | np19 8lr | np198lr | Newport | Casnewydd | Caerleon Road STW | 1370 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332586 | 188763 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LS | NP198LS | np19 8ls | np198ls | Newport | Casnewydd | Caerleon Road STW | 1354 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332685 | 188657 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LT | NP198LT | np19 8lt | np198lt | Newport | Casnewydd | Caerleon Road STW | 1407 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332642 | 188626 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LU | NP198LU | np19 8lu | np198lu | Newport | Casnewydd | Caerleon Road STW | 1239 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332770 | 188735 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LW | NP198LW | np19 8lw | np198lw | Newport | Casnewydd | Caerleon Road STW | 1294 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332693 | 188744 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LX | NP198LX | np19 8lx | np198lx | Newport | Casnewydd | Caerleon Road STW | 1121 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332905 | 188761 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LY | NP198LY | np19 8ly | np198ly | Newport | Casnewydd | Caerleon Road STW | 1096 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332991 | 188712 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8LZ | NP198LZ | np19 8lz | np198lz | Newport | Casnewydd | Caerleon Road STW | 1038 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333130 | 188677 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NA | NP198NA | np19 8na | np198na | Newport | Casnewydd | Caerleon Road STW | 1233 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 333017 | 188517 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NB | NP198NB | np19 8nb | np198nb | Newport | Casnewydd | Caerleon Road STW | 1210 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332989 | 188566 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8ND | NP198ND | np19 8nd | np198nd | Newport | Casnewydd | Caerleon Road STW | 1308 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332904 | 188508 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NE | NP198NE | np19 8ne | np198ne | Newport | Casnewydd | Caerleon Road STW | 1169 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332966 | 188637 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NF | NP198NF | np19 8nf | np198nf | Newport | Casnewydd | Caerleon Road STW | 1393 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332892 | 188411 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NL | NP198NL | np19 8nl | np198nl | Newport | Casnewydd | Caerleon Road STW | 1668 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332691 | 188218 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NN | NP198NN | np19 8nn | np198nn | Newport | Casnewydd | Caerleon Road STW | 1645 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332788 | 188175 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NP | NP198NP | np19 8np | np198np | Newport | Casnewydd | Caerleon Road STW | 1578 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332959 | 188148 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NQ | NP198NQ | np19 8nq | np198nq | Newport | Casnewydd | Caerleon Road STW | 1552 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333046 | 188133 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NR | NP198NR | np19 8nr | np198nr | Newport | Casnewydd | Caerleon Road STW | 1660 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332996 | 188037 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NS | NP198NS | np19 8ns | np198ns | Newport | Casnewydd | Caerleon Road STW | 1663 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332971 | 188046 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NT | NP198NT | np19 8nt | np198nt | Newport | Casnewydd | Caerleon Road STW | 1764 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332896 | 187971 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NU | NP198NU | np19 8nu | np198nu | Newport | Casnewydd | Caerleon Road STW | 1668 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332939 | 188057 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NW | NP198NW | np19 8nw | np198nw | Newport | Casnewydd | Caerleon Road STW | 1781 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332789 | 188013 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NX | NP198NX | np19 8nx | np198nx | Newport | Casnewydd | Caerleon Road STW | 1671 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332881 | 188086 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NY | NP198NY | np19 8ny | np198ny | Newport | Casnewydd | Caerleon Road STW | 1687 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332823 | 188102 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8NZ | NP198NZ | np19 8nz | np198nz | Newport | Casnewydd | Caerleon Road STW | 1716 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332740 | 188122 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8PA | NP198PA | np19 8pa | np198pa | Newport | Casnewydd | Caerleon Road STW | 1803 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332675 | 188061 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8PB | NP198PB | np19 8pb | np198pb | Newport | Casnewydd | Caerleon Road STW | 1728 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332685 | 188147 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8PD | NP198PD | np19 8pd | np198pd | Newport | Casnewydd | Caerleon Road STW | 1744 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 332649 | 188154 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8PE | NP198PE | np19 8pe | np198pe | Newport | Casnewydd | Caerleon Road STW | 1390 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 332555 | 188773 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8WU | NP198WU | np19 8wu | np198wu | Newport | Casnewydd | Caerleon Road STW | 2208 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331808 | 188427 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8XA | NP198XA | np19 8xa | np198xa | Newport | Casnewydd | Caerleon Road STW | 1980 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 332124 | 188360 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 8XR | NP198XR | np19 8xr | np198xr | Newport | Casnewydd | Caerleon Road STW | 1435 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333310 | 188155 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AA | NP199AA | np19 9aa | np199aa | Newport | Casnewydd | Caerleon Road STW | 1520 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333531 | 188022 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AB | NP199AB | np19 9ab | np199ab | Newport | Casnewydd | Caerleon Road STW | 1555 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333588 | 187981 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AD | NP199AD | np19 9ad | np199ad | Newport | Casnewydd | Caerleon Road STW | 1588 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333437 | 187968 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AE | NP199AE | np19 9ae | np199ae | Newport | Casnewydd | Caerleon Road STW | 1707 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333418 | 187851 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AF | NP199AF | np19 9af | np199af | Newport | Casnewydd | Caerleon Road STW | 1638 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333444 | 187916 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AG | NP199AG | np19 9ag | np199ag | Newport | Casnewydd | Caerleon Road STW | 1738 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 333443 | 187815 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AH | NP199AH | np19 9ah | np199ah | Newport | Casnewydd | Caerleon Road STW | 1616 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333585 | 187920 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AJ | NP199AJ | np19 9aj | np199aj | Newport | Casnewydd | Caerleon Road STW | 1539 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333726 | 187992 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AL | NP199AL | np19 9al | np199al | Newport | Casnewydd | Caerleon Road STW | 1708 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333563 | 187830 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AN | NP199AN | np19 9an | np199an | Newport | Casnewydd | Caerleon Road STW | 1582 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333769 | 187949 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AP | NP199AP | np19 9ap | np199ap | Newport | Casnewydd | Caerleon Road STW | 1829 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333666 | 187702 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AQ | NP199AQ | np19 9aq | np199aq | Newport | Casnewydd | Caerleon Road STW | 1772 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333712 | 187759 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AR | NP199AR | np19 9ar | np199ar | Newport | Casnewydd | Caerleon Road STW | 1869 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334551 | 187857 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AS | NP199AS | np19 9as | np199as | Newport | Casnewydd | Caerleon Road STW | 1519 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333870 | 188019 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AT | NP199AT | np19 9at | np199at | Newport | Casnewydd | Caerleon Road STW | 1445 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333751 | 188086 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AU | NP199AU | np19 9au | np199au | Newport | Casnewydd | Caerleon Road STW | 1427 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333802 | 188106 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AW | NP199AW | np19 9aw | np199aw | Newport | Casnewydd | Caerleon Road STW | 1398 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333773 | 188133 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AX | NP199AX | np19 9ax | np199ax | Newport | Casnewydd | Caerleon Road STW | 1443 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333731 | 188088 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AY | NP199AY | np19 9ay | np199ay | Newport | Casnewydd | Caerleon Road STW | 1404 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333652 | 188128 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9AZ | NP199AZ | np19 9az | np199az | Newport | Casnewydd | Caerleon Road STW | 1452 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333645 | 188080 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BA | NP199BA | np19 9ba | np199ba | Newport | Casnewydd | Christchurch WwTW | 1293 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334818 | 188819 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BB | NP199BB | np19 9bb | np199bb | Newport | Casnewydd | Caerleon Road STW | 1254 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334735 | 188795 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BD | NP199BD | np19 9bd | np199bd | Newport | Casnewydd | Caerleon Road STW | 1706 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333530 | 187835 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BG | NP199BG | np19 9bg | np199bg | Newport | Casnewydd | Caerleon Road STW | 1299 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334750 | 188740 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BH | NP199BH | np19 9bh | np199bh | Newport | Casnewydd | Caerleon Road STW | 1377 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333542 | 188165 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BJ | NP199BJ | np19 9bj | np199bj | Newport | Casnewydd | Caerleon Road STW | 1295 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333704 | 188236 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BL | NP199BL | np19 9bl | np199bl | Newport | Casnewydd | Caerleon Road STW | 1231 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333942 | 188320 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BN | NP199BN | np19 9bn | np199bn | Newport | Casnewydd | Caerleon Road STW | 1163 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334117 | 188437 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BP | NP199BP | np19 9bp | np199bp | Newport | Casnewydd | Caerleon Road STW | 1133 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334085 | 188458 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BQ | NP199BQ | np19 9bq | np199bq | Newport | Casnewydd | Caerleon Road STW | 1217 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333733 | 188313 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BR | NP199BR | np19 9br | np199br | Newport | Casnewydd | Caerleon Road STW | 1151 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333933 | 188399 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BS | NP199BS | np19 9bs | np199bs | Newport | Casnewydd | Caerleon Road STW | 1004 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334157 | 188627 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BT | NP199BT | np19 9bt | np199bt | Newport | Casnewydd | Caerleon Road STW | 1036 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334241 | 188635 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BU | NP199BU | np19 9bu | np199bu | Newport | Casnewydd | Caerleon Road STW | 1074 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334164 | 188552 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BW | NP199BW | np19 9bw | np199bw | Newport | Casnewydd | Caerleon Road STW | 1093 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334281 | 188592 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BX | NP199BX | np19 9bx | np199bx | Newport | Casnewydd | Caerleon Road STW | 1006 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334313 | 188718 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BY | NP199BY | np19 9by | np199by | Newport | Casnewydd | Caerleon Road STW | 1122 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334411 | 188646 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9BZ | NP199BZ | np19 9bz | np199bz | Newport | Casnewydd | Caerleon Road STW | 1172 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334336 | 188534 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DA | NP199DA | np19 9da | np199da | Newport | Casnewydd | Caerleon Road STW | 1205 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334142 | 188402 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DB | NP199DB | np19 9db | np199db | Newport | Casnewydd | Caerleon Road STW | 1272 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333955 | 188280 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DD | NP199DD | np19 9dd | np199dd | Newport | Casnewydd | Caerleon Road STW | 1287 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333829 | 188248 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DE | NP199DE | np19 9de | np199de | Newport | Casnewydd | Caerleon Road STW | 1303 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333777 | 188229 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DF | NP199DF | np19 9df | np199df | Newport | Casnewydd | Caerleon Road STW | 1041 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334415 | 188756 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DG | NP199DG | np19 9dg | np199dg | Newport | Casnewydd | Caerleon Road STW | 1350 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333673 | 188181 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DH | NP199DH | np19 9dh | np199dh | Newport | Casnewydd | Caerleon Road STW | 1079 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334383 | 188679 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DJ | NP199DJ | np19 9dj | np199dj | Newport | Casnewydd | Caerleon Road STW | 1090 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334533 | 188805 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DL | NP199DL | np19 9dl | np199dl | Newport | Casnewydd | Caerleon Road STW | 1031 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334492 | 188847 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DN | NP199DN | np19 9dn | np199dn | Newport | Casnewydd | Christchurch WwTW | 1250 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334873 | 188937 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DP | NP199DP | np19 9dp | np199dp | Newport | Casnewydd | Christchurch WwTW | 1128 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334813 | 189055 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DQ | NP199DQ | np19 9dq | np199dq | Newport | Casnewydd | Christchurch WwTW | 1182 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334922 | 189110 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DR | NP199DR | np19 9dr | np199dr | Newport | Casnewydd | Christchurch WwTW | 1235 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335009 | 189151 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DS | NP199DS | np19 9ds | np199ds | Newport | Casnewydd | Christchurch WwTW | 1314 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335052 | 189069 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DT | NP199DT | np19 9dt | np199dt | Newport | Casnewydd | Christchurch WwTW | 1261 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334958 | 189024 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DU | NP199DU | np19 9du | np199du | Newport | Casnewydd | Caerleon Road STW | 950 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334369 | 188837 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DW | NP199DW | np19 9dw | np199dw | Newport | Casnewydd | Caerleon Road STW | 1348 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334636 | 188541 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DX | NP199DX | np19 9dx | np199dx | Newport | Casnewydd | Caerleon Road STW | 1321 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334671 | 188614 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DY | NP199DY | np19 9dy | np199dy | Newport | Casnewydd | Caerleon Road STW | 1355 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334743 | 188642 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9DZ | NP199DZ | np19 9dz | np199dz | Newport | Casnewydd | Caerleon Road STW | 1234 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334599 | 188665 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9EA | NP199EA | np19 9ea | np199ea | Newport | Casnewydd | Caerleon Road STW | 1411 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334623 | 188447 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9EB | NP199EB | np19 9eb | np199eb | Newport | Casnewydd | Caerleon Road STW | 1292 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334419 | 188444 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9ED | NP199ED | np19 9ed | np199ed | Newport | Casnewydd | Caerleon Road STW | 1538 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334762 | 188400 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9EE | NP199EE | np19 9ee | np199ee | Newport | Casnewydd | Caerleon Road STW | 1490 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334767 | 188470 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9EF | NP199EF | np19 9ef | np199ef | Newport | Casnewydd | Caerleon Road STW | 1380 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334793 | 188663 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9EN | NP199EN | np19 9en | np199en | Newport | Casnewydd | Caerleon Road STW | 1365 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334787 | 188679 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9EP | NP199EP | np19 9ep | np199ep | Newport | Casnewydd | Caerleon Road STW | 1502 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334723 | 188412 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9EQ | NP199EQ | np19 9eq | np199eq | Newport | Casnewydd | Christchurch WwTW | 1161 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334951 | 189199 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9ER | NP199ER | np19 9er | np199er | Newport | Casnewydd | Christchurch WwTW | 1060 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334694 | 189023 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9ES | NP199ES | np19 9es | np199es | Newport | Casnewydd | Christchurch WwTW | 1112 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334761 | 189018 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9ET | NP199ET | np19 9et | np199et | Newport | Casnewydd | Caerleon Road STW | 1187 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334686 | 188841 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9EU | NP199EU | np19 9eu | np199eu | Newport | Casnewydd | Christchurch WwTW | 1192 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334801 | 188944 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9EW | NP199EW | np19 9ew | np199ew | Newport | Casnewydd | Caerleon Road STW | 1134 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334652 | 188884 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9EX | NP199EX | np19 9ex | np199ex | Newport | Casnewydd | Caerleon Road STW | 1163 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 334474 | 188645 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9EY | NP199EY | np19 9ey | np199ey | Newport | Casnewydd | Caerleon Road STW | 1196 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334582 | 188702 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9EZ | NP199EZ | np19 9ez | np199ez | Newport | Casnewydd | Christchurch WwTW | 1200 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334729 | 188865 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9FA | NP199FA | np19 9fa | np199fa | Newport | Casnewydd | Christchurch WwTW | 1156 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334680 | 188881 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9FB | NP199FB | np19 9fb | np199fb | Newport | Casnewydd | Christchurch WwTW | 1317 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334894 | 188861 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9FL | NP199FL | np19 9fl | np199fl | Newport | Casnewydd | Christchurch WwTW | 1385 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335140 | 189077 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9FN | NP199FN | np19 9fn | np199fn | Newport | Casnewydd | Christchurch WwTW | 1415 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335169 | 189067 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9FP | NP199FP | np19 9fp | np199fp | Newport | Casnewydd | Ponthir STW | 1494 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335278 | 189070 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9FQ | NP199FQ | np19 9fq | np199fq | Newport | Casnewydd | Christchurch WwTW | 1609 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335332 | 188962 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9FR | NP199FR | np19 9fr | np199fr | Newport | Casnewydd | Ponthir STW | 1654 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335388 | 188945 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9FS | NP199FS | np19 9fs | np199fs | Newport | Casnewydd | Ponthir STW | 1708 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335482 | 188933 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9FT | NP199FT | np19 9ft | np199ft | Newport | Casnewydd | Christchurch WwTW | 1623 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335286 | 188863 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9FU | NP199FU | np19 9fu | np199fu | Newport | Casnewydd | Christchurch WwTW | 1669 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335331 | 188846 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GA | NP199GA | np19 9ga | np199ga | Newport | Casnewydd | Caerleon Road STW | 1095 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334554 | 188821 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GF | NP199GF | np19 9gf | np199gf | Newport | Casnewydd | Ponthir STW | 1561 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335420 | 189067 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GG | NP199GG | np19 9gg | np199gg | Newport | Casnewydd | Ponthir STW | 1648 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335597 | 189075 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GH | NP199GH | np19 9gh | np199gh | Newport | Casnewydd | Ponthir STW | 1591 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335521 | 189093 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GJ | NP199GJ | np19 9gj | np199gj | Newport | Casnewydd | Ponthir STW | 1517 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335465 | 189145 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GL | NP199GL | np19 9gl | np199gl | Newport | Casnewydd | Ponthir STW | 1541 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335552 | 189174 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GN | NP199GN | np19 9gn | np199gn | Newport | Casnewydd | Ponthir STW | 1441 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335412 | 189201 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GP | NP199GP | np19 9gp | np199gp | Newport | Casnewydd | Ponthir STW | 1466 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335554 | 189269 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GQ | NP199GQ | np19 9gq | np199gq | Newport | Casnewydd | Ponthir STW | 1478 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335632 | 189317 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GR | NP199GR | np19 9gr | np199gr | Newport | Casnewydd | Ponthir STW | 1616 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335768 | 189255 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GS | NP199GS | np19 9gs | np199gs | Newport | Casnewydd | Ponthir STW | 1617 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335800 | 189284 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GT | NP199GT | np19 9gt | np199gt | Newport | Casnewydd | Ponthir STW | 1797 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335830 | 189067 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GU | NP199GU | np19 9gu | np199gu | Newport | Casnewydd | Ponthir STW | 1784 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335858 | 189109 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GW | NP199GW | np19 9gw | np199gw | Newport | Casnewydd | Ponthir STW | 1947 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335919 | 188946 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GX | NP199GX | np19 9gx | np199gx | Newport | Casnewydd | Ponthir STW | 1998 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335948 | 188903 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GY | NP199GY | np19 9gy | np199gy | Newport | Casnewydd | Ponthir STW | 1685 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335745 | 189142 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9GZ | NP199GZ | np19 9gz | np199gz | Newport | Casnewydd | Ponthir STW | 1578 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335681 | 189227 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HA | NP199HA | np19 9ha | np199ha | Newport | Casnewydd | Ponthir STW | 1723 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335694 | 189053 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HB | NP199HB | np19 9hb | np199hb | Newport | Casnewydd | Ponthir STW | 1797 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335726 | 188984 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HE | NP199HE | np19 9he | np199he | Newport | Casnewydd | Ponthir STW | 1812 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335640 | 188907 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HF | NP199HF | np19 9hf | np199hf | Newport | Casnewydd | Ponthir STW | 1807 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335635 | 188909 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HG | NP199HG | np19 9hg | np199hg | Newport | Casnewydd | Ponthir STW | 1880 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335654 | 188835 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HH | NP199HH | np19 9hh | np199hh | Newport | Casnewydd | Ponthir STW | 1770 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335663 | 188972 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HJ | NP199HJ | np19 9hj | np199hj | Newport | Casnewydd | Caerleon Road STW | 1594 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334874 | 188431 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HP | NP199HP | np19 9hp | np199hp | Newport | Casnewydd | Caerleon Road STW | 2138 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335268 | 188056 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HQ | NP199HQ | np19 9hq | np199hq | Newport | Casnewydd | Ponthir STW | 1817 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335635 | 188897 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HR | NP199HR | np19 9hr | np199hr | Newport | Casnewydd | Christchurch WwTW | 2353 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335757 | 188275 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HS | NP199HS | np19 9hs | np199hs | Newport | Casnewydd | Christchurch WwTW | 2296 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335763 | 188373 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HT | NP199HT | np19 9ht | np199ht | Newport | Casnewydd | Ponthir STW | 2247 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335845 | 188522 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HU | NP199HU | np19 9hu | np199hu | Newport | Casnewydd | Christchurch WwTW | 2386 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335856 | 188347 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HW | NP199HW | np19 9hw | np199hw | Newport | Casnewydd | Ponthir STW | 2401 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335918 | 188386 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HX | NP199HX | np19 9hx | np199hx | Newport | Casnewydd | Ponthir STW | 2436 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 336027 | 188415 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HY | NP199HY | np19 9hy | np199hy | Newport | Casnewydd | Ponthir STW | 2295 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335979 | 188553 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9HZ | NP199HZ | np19 9hz | np199hz | Newport | Casnewydd | Ponthir STW | 2306 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335915 | 188496 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JA | NP199JA | np19 9ja | np199ja | Newport | Casnewydd | Ponthir STW | 2239 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335980 | 188623 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JB | NP199JB | np19 9jb | np199jb | Newport | Casnewydd | Ponthir STW | 2294 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 336036 | 188596 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JD | NP199JD | np19 9jd | np199jd | Newport | Casnewydd | Ponthir STW | 2415 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 336067 | 188468 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JE | NP199JE | np19 9je | np199je | Newport | Casnewydd | Ponthir STW | 2350 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 336096 | 188571 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JF | NP199JF | np19 9jf | np199jf | Newport | Casnewydd | Ponthir STW | 2279 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 336066 | 188637 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JG | NP199JG | np19 9jg | np199jg | Newport | Casnewydd | Ponthir STW | 2212 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 336040 | 188702 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JH | NP199JH | np19 9jh | np199jh | Newport | Casnewydd | Ponthir STW | 2120 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335983 | 188774 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JJ | NP199JJ | np19 9jj | np199jj | Newport | Casnewydd | Ponthir STW | 2102 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335905 | 188737 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JL | NP199JL | np19 9jl | np199jl | Newport | Casnewydd | Ponthir STW | 2020 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335836 | 188789 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JN | NP199JN | np19 9jn | np199jn | Newport | Casnewydd | Ponthir STW | 2089 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335969 | 188803 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JP | NP199JP | np19 9jp | np199jp | Newport | Casnewydd | Ponthir STW | 2018 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335772 | 188747 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JQ | NP199JQ | np19 9jq | np199jq | Newport | Casnewydd | Ponthir STW | 1949 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335777 | 188834 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JR | NP199JR | np19 9jr | np199jr | Newport | Casnewydd | Ponthir STW | 2083 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335747 | 188654 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JS | NP199JS | np19 9js | np199js | Newport | Casnewydd | Ponthir STW | 2470 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 336015 | 188366 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9JT | NP199JT | np19 9jt | np199jt | Newport | Casnewydd | Ponthir STW | 1999 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 335788 | 188780 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LA | NP199LA | np19 9la | np199la | Newport | Casnewydd | Caerleon Road STW | 2159 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335328 | 188091 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LD | NP199LD | np19 9ld | np199ld | Newport | Casnewydd | Christchurch WwTW | 2256 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335517 | 188156 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LE | NP199LE | np19 9le | np199le | Newport | Casnewydd | Caerleon Road STW | 2064 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335088 | 187986 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LF | NP199LF | np19 9lf | np199lf | Newport | Casnewydd | Caerleon Road STW | 2095 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335141 | 187991 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LG | NP199LG | np19 9lg | np199lg | Newport | Casnewydd | Caerleon Road STW | 2037 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335140 | 188071 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LH | NP199LH | np19 9lh | np199lh | Newport | Casnewydd | Caerleon Road STW | 2148 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335356 | 188140 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LJ | NP199LJ | np19 9lj | np199lj | Newport | Casnewydd | Christchurch WwTW | 2306 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335601 | 188170 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LL | NP199LL | np19 9ll | np199ll | Newport | Casnewydd | Christchurch WwTW | 2311 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335649 | 188213 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LN | NP199LN | np19 9ln | np199ln | Newport | Casnewydd | Christchurch WwTW | 2360 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335711 | 188209 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LP | NP199LP | np19 9lp | np199lp | Newport | Casnewydd | Christchurch WwTW | 2273 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335629 | 188248 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LQ | NP199LQ | np19 9lq | np199lq | Newport | Casnewydd | Christchurch WwTW | 2238 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335614 | 188284 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LR | NP199LR | np19 9lr | np199lr | Newport | Casnewydd | Christchurch WwTW | 2111 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335396 | 188240 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LS | NP199LS | np19 9ls | np199ls | Newport | Casnewydd | Caerleon Road STW | 1959 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334983 | 188033 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LT | NP199LT | np19 9lt | np199lt | Newport | Casnewydd | Caerleon Road STW | 1822 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335001 | 188235 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LU | NP199LU | np19 9lu | np199lu | Newport | Casnewydd | Caerleon Road STW | 1962 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335117 | 188153 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LW | NP199LW | np19 9lw | np199lw | Newport | Casnewydd | Caerleon Road STW | 2077 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335302 | 188185 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LX | NP199LX | np19 9lx | np199lx | Newport | Casnewydd | Christchurch WwTW | 2080 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335486 | 188378 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LY | NP199LY | np19 9ly | np199ly | Newport | Casnewydd | Christchurch WwTW | 1937 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335310 | 188400 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9LZ | NP199LZ | np19 9lz | np199lz | Newport | Casnewydd | Christchurch WwTW | 2047 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335466 | 188405 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NA | NP199NA | np19 9na | np199na | Newport | Casnewydd | Christchurch WwTW | 2073 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335577 | 188497 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NB | NP199NB | np19 9nb | np199nb | Newport | Casnewydd | Christchurch WwTW | 2107 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 335593 | 188463 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9ND | NP199ND | np19 9nd | np199nd | Newport | Casnewydd | Christchurch WwTW | 2009 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335471 | 188468 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NE | NP199NE | np19 9ne | np199ne | Newport | Casnewydd | Caerleon Road STW | 1823 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335158 | 188411 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NF | NP199NF | np19 9nf | np199nf | Newport | Casnewydd | Caerleon Road STW | 2066 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335159 | 188048 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NG | NP199NG | np19 9ng | np199ng | Newport | Casnewydd | Christchurch WwTW | 1468 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334912 | 188668 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NH | NP199NH | np19 9nh | np199nh | Newport | Casnewydd | Caerleon Road STW | 1513 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334911 | 188597 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NJ | NP199NJ | np19 9nj | np199nj | Newport | Casnewydd | Christchurch WwTW | 1523 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334963 | 188641 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NL | NP199NL | np19 9nl | np199nl | Newport | Casnewydd | Christchurch WwTW | 1389 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334908 | 188773 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NN | NP199NN | np19 9nn | np199nn | Newport | Casnewydd | Caerleon Road STW | 1483 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334862 | 188585 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NP | NP199NP | np19 9np | np199np | Newport | Casnewydd | Christchurch WwTW | 1519 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335008 | 188688 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NQ | NP199NQ | np19 9nq | np199nq | Newport | Casnewydd | Caerleon Road STW | 1416 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334854 | 188682 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NR | NP199NR | np19 9nr | np199nr | Newport | Casnewydd | Christchurch WwTW | 1418 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334883 | 188709 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NS | NP199NS | np19 9ns | np199ns | Newport | Casnewydd | Caerleon Road STW | 1879 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334573 | 187857 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NT | NP199NT | np19 9nt | np199nt | Newport | Casnewydd | Caerleon Road STW | 1828 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334648 | 187956 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NX | NP199NX | np19 9nx | np199nx | Newport | Casnewydd | Caerleon Road STW | 1831 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334710 | 187990 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NY | NP199NY | np19 9ny | np199ny | Newport | Casnewydd | Caerleon Road STW | 1777 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334748 | 188081 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9NZ | NP199NZ | np19 9nz | np199nz | Newport | Casnewydd | Caerleon Road STW | 1966 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334818 | 187900 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PA | NP199PA | np19 9pa | np199pa | Newport | Casnewydd | Caerleon Road STW | 1886 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334879 | 188043 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PB | NP199PB | np19 9pb | np199pb | Newport | Casnewydd | Caerleon Road STW | 1999 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334921 | 187933 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PD | NP199PD | np19 9pd | np199pd | Newport | Casnewydd | Caerleon Road STW | 2077 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335011 | 187904 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PE | NP199PE | np19 9pe | np199pe | Newport | Casnewydd | Caerleon Road STW | 2022 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334977 | 187947 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PF | NP199PF | np19 9pf | np199pf | Newport | Casnewydd | Caerleon Road STW | 1999 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334974 | 187974 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PG | NP199PG | np19 9pg | np199pg | Newport | Casnewydd | Caerleon Road STW | 1815 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334873 | 188129 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PH | NP199PH | np19 9ph | np199ph | Newport | Casnewydd | Caerleon Road STW | 1651 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334805 | 188286 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PJ | NP199PJ | np19 9pj | np199pj | Newport | Casnewydd | Caerleon Road STW | 1629 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334827 | 188336 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PL | NP199PL | np19 9pl | np199pl | Newport | Casnewydd | Caerleon Road STW | 1653 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334976 | 188456 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PN | NP199PN | np19 9pn | np199pn | Newport | Casnewydd | Caerleon Road STW | 1697 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 335001 | 188418 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PP | NP199PP | np19 9pp | np199pp | Newport | Casnewydd | Christchurch WwTW | 1662 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335109 | 188588 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PQ | NP199PQ | np19 9pq | np199pq | Newport | Casnewydd | Christchurch WwTW | 1732 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335175 | 188554 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PR | NP199PR | np19 9pr | np199pr | Newport | Casnewydd | Christchurch WwTW | 1765 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335293 | 188636 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PS | NP199PS | np19 9ps | np199ps | Newport | Casnewydd | Christchurch WwTW | 1821 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335442 | 188739 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PT | NP199PT | np19 9pt | np199pt | Newport | Casnewydd | Caerleon Road STW | 1871 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334681 | 187925 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PU | NP199PU | np19 9pu | np199pu | Newport | Casnewydd | Caerleon Road STW | 1891 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334718 | 187924 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PW | NP199PW | np19 9pw | np199pw | Newport | Casnewydd | Caerleon Road STW | 1949 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334723 | 187860 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PX | NP199PX | np19 9px | np199px | Newport | Casnewydd | Caerleon Road STW | 1920 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334637 | 187844 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9PZ | NP199PZ | np19 9pz | np199pz | Newport | Casnewydd | Caerleon Road STW | 1467 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333888 | 188073 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QA | NP199QA | np19 9qa | np199qa | Newport | Casnewydd | Caerleon Road STW | 1394 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334181 | 188215 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QB | NP199QB | np19 9qb | np199qb | Newport | Casnewydd | Caerleon Road STW | 1704 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333854 | 187832 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QD | NP199QD | np19 9qd | np199qd | Newport | Casnewydd | Caerleon Road STW | 1549 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334069 | 188021 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QE | NP199QE | np19 9qe | np199qe | Newport | Casnewydd | Caerleon Road STW | 1331 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334238 | 188304 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QF | NP199QF | np19 9qf | np199qf | Newport | Casnewydd | Caerleon Road STW | 1481 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333895 | 188060 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QG | NP199QG | np19 9qg | np199qg | Newport | Casnewydd | Caerleon Road STW | 1470 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333958 | 188080 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QH | NP199QH | np19 9qh | np199qh | Newport | Casnewydd | Caerleon Road STW | 1357 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334074 | 188220 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QJ | NP199QJ | np19 9qj | np199qj | Newport | Casnewydd | Caerleon Road STW | 1492 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 333991 | 188063 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QL | NP199QL | np19 9ql | np199ql | Newport | Casnewydd | Caerleon Road STW | 1504 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334028 | 188058 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QN | NP199QN | np19 9qn | np199qn | Newport | Casnewydd | Caerleon Road STW | 1554 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334021 | 188006 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QP | NP199QP | np19 9qp | np199qp | Newport | Casnewydd | Caerleon Road STW | 1742 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334057 | 187822 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QQ | NP199QQ | np19 9qq | np199qq | Newport | Casnewydd | Caerleon Road STW | 1787 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334272 | 187831 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QR | NP199QR | np19 9qr | np199qr | Newport | Casnewydd | Caerleon Road STW | 1904 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334301 | 187718 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QS | NP199QS | np19 9qs | np199qs | Newport | Casnewydd | Caerleon Road STW | 1930 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334537 | 187782 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QT | NP199QT | np19 9qt | np199qt | Newport | Casnewydd | Caerleon Road STW | 1916 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334418 | 187746 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QU | NP199QU | np19 9qu | np199qu | Newport | Casnewydd | Caerleon Road STW | 1962 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334352 | 187673 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QW | NP199QW | np19 9qw | np199qw | Newport | Casnewydd | Caerleon Road STW | 2022 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334467 | 187652 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QX | NP199QX | np19 9qx | np199qx | Newport | Casnewydd | Caerleon Road STW | 1948 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334460 | 187729 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QY | NP199QY | np19 9qy | np199qy | Newport | Casnewydd | Caerleon Road STW | 1960 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334547 | 187754 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9QZ | NP199QZ | np19 9qz | np199qz | Newport | Casnewydd | Caerleon Road STW | 2036 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334555 | 187674 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RA | NP199RA | np19 9ra | np199ra | Newport | Casnewydd | Caerleon Road STW | 2031 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334594 | 187698 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RB | NP199RB | np19 9rb | np199rb | Newport | Casnewydd | Caerleon Road STW | 2009 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334650 | 187750 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RD | NP199RD | np19 9rd | np199rd | Newport | Casnewydd | Caerleon Road STW | 1979 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334670 | 187795 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RE | NP199RE | np19 9re | np199re | Newport | Casnewydd | Caerleon Road STW | 2041 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334718 | 187750 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RF | NP199RF | np19 9rf | np199rf | Newport | Casnewydd | Caerleon Road STW | 2013 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334775 | 187817 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RG | NP199RG | np19 9rg | np199rg | Newport | Casnewydd | Caerleon Road STW | 2025 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334897 | 187883 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RH | NP199RH | np19 9rh | np199rh | Newport | Casnewydd | Caerleon Road STW | 2080 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334831 | 187772 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RJ | NP199RJ | np19 9rj | np199rj | Newport | Casnewydd | Caerleon Road STW | 2055 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334487 | 187624 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RU | NP199RU | np19 9ru | np199ru | Newport | Casnewydd | Caerleon Road STW | 1851 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334273 | 187764 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RW | NP199RW | np19 9rw | np199rw | Newport | Casnewydd | Caerleon Road STW | 1778 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334355 | 187870 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RX | NP199RX | np19 9rx | np199rx | Newport | Casnewydd | Caerleon Road STW | 1759 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334449 | 187930 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RY | NP199RY | np19 9ry | np199ry | Newport | Casnewydd | Caerleon Road STW | 1767 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334498 | 187944 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9RZ | NP199RZ | np19 9rz | np199rz | Newport | Casnewydd | Caerleon Road STW | 1734 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334691 | 188094 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SA | NP199SA | np19 9sa | np199sa | Newport | Casnewydd | Caerleon Road STW | 1728 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334602 | 188045 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SB | NP199SB | np19 9sb | np199sb | Newport | Casnewydd | Caerleon Road STW | 1664 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334689 | 188178 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SD | NP199SD | np19 9sd | np199sd | Newport | Casnewydd | Caerleon Road STW | 1556 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334669 | 188298 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SE | NP199SE | np19 9se | np199se | Newport | Casnewydd | Caerleon Road STW | 1448 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334527 | 188328 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SF | NP199SF | np19 9sf | np199sf | Newport | Casnewydd | Caerleon Road STW | 1582 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334631 | 188237 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SG | NP199SG | np19 9sg | np199sg | Newport | Casnewydd | Caerleon Road STW | 1524 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334474 | 188206 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SH | NP199SH | np19 9sh | np199sh | Newport | Casnewydd | Caerleon Road STW | 1663 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334464 | 188043 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SJ | NP199SJ | np19 9sj | np199sj | Newport | Casnewydd | Caerleon Road STW | 1546 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334428 | 188156 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SL | NP199SL | np19 9sl | np199sl | Newport | Casnewydd | Caerleon Road STW | 1510 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334307 | 188139 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SN | NP199SN | np19 9sn | np199sn | Newport | Casnewydd | Caerleon Road STW | 1450 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334252 | 188182 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SP | NP199SP | np19 9sp | np199sp | Newport | Casnewydd | Caerleon Road STW | 1413 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334329 | 188256 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SQ | NP199SQ | np19 9sq | np199sq | Newport | Casnewydd | Caerleon Road STW | 1513 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334167 | 188085 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SR | NP199SR | np19 9sr | np199sr | Newport | Casnewydd | Caerleon Road STW | 1539 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334305 | 188107 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SS | NP199SS | np19 9ss | np199ss | Newport | Casnewydd | Caerleon Road STW | 1611 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334310 | 188032 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9ST | NP199ST | np19 9st | np199st | Newport | Casnewydd | Caerleon Road STW | 1579 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334542 | 188183 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SU | NP199SU | np19 9su | np199su | Newport | Casnewydd | Caerleon Road STW | 1625 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334588 | 188157 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SX | NP199SX | np19 9sx | np199sx | Newport | Casnewydd | Caerleon Road STW | 1688 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 334607 | 188095 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SY | NP199SY | np19 9sy | np199sy | Newport | Casnewydd | Caerleon Road STW | 1717 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334394 | 187952 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9SZ | NP199SZ | np19 9sz | np199sz | Newport | Casnewydd | Caerleon Road STW | 1743 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 334276 | 187879 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9TA | NP199TA | np19 9ta | np199ta | Newport | Casnewydd | Christchurch WwTW | 1426 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335104 | 188945 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9TB | NP199TB | np19 9tb | np199tb | Newport | Casnewydd | Christchurch WwTW | 1339 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 334971 | 188914 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9TD | NP199TD | np19 9td | np199td | Newport | Casnewydd | Christchurch WwTW | 1460 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335049 | 188819 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9TE | NP199TE | np19 9te | np199te | Newport | Casnewydd | Christchurch WwTW | 1515 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335182 | 188901 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9TF | NP199TF | np19 9tf | np199tf | Newport | Casnewydd | Christchurch WwTW | 1442 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335005 | 188797 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9TG | NP199TG | np19 9tg | np199tg | Newport | Casnewydd | Christchurch WwTW | 1563 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335229 | 188885 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9TH | NP199TH | np19 9th | np199th | Newport | Casnewydd | Christchurch WwTW | 1484 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335120 | 188869 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9TJ | NP199TJ | np19 9tj | np199tj | Newport | Casnewydd | Christchurch WwTW | 1536 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335244 | 188957 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9TL | NP199TL | np19 9tl | np199tl | Newport | Casnewydd | Christchurch WwTW | 1422 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335128 | 188988 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9TN | NP199TN | np19 9tn | np199tn | Newport | Casnewydd | Christchurch WwTW | 1450 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335073 | 188864 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9TP | NP199TP | np19 9tp | np199tp | Newport | Casnewydd | Christchurch WwTW | 1548 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335112 | 188757 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP19 9TQ | NP199TQ | np19 9tq | np199tq | Newport | Casnewydd | Christchurch WwTW | 1545 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 335087 | 188734 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1AA | NP201AA | np20 1aa | np201aa | Newport | Casnewydd | Caerleon Road STW | 2963 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331005 | 188347 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1AB | NP201AB | np20 1ab | np201ab | Newport | Casnewydd | Caerleon Road STW | 2982 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331066 | 188173 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1AD | NP201AD | np20 1ad | np201ad | Newport | Casnewydd | Caerleon Road STW | 2877 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331111 | 188319 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1AE | NP201AE | np20 1ae | np201ae | Newport | Casnewydd | Caerleon Road STW | 3081 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331108 | 187898 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1AF | NP201AF | np20 1af | np201af | Newport | Casnewydd | Caerleon Road STW | 2910 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331401 | 187774 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1AG | NP201AG | np20 1ag | np201ag | Newport | Casnewydd | Caerleon Road STW | 3081 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331108 | 187898 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DA | NP201DA | np20 1da | np201da | Newport | Casnewydd | Caerleon Road STW | 2879 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331109 | 188320 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DB | NP201DB | np20 1db | np201db | Newport | Casnewydd | Caerleon Road STW | 2899 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331111 | 188268 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DD | NP201DD | np20 1dd | np201dd | Newport | Casnewydd | Caerleon Road STW | 2952 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331055 | 188263 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DF | NP201DF | np20 1df | np201df | Newport | Casnewydd | Caerleon Road STW | 2898 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331138 | 188216 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DG | NP201DG | np20 1dg | np201dg | Newport | Casnewydd | Caerleon Road STW | 2915 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331117 | 188221 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DH | NP201DH | np20 1dh | np201dh | Newport | Casnewydd | Caerleon Road STW | 2917 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331147 | 188158 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DJ | NP201DJ | np20 1dj | np201dj | Newport | Casnewydd | Caerleon Road STW | 2897 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331169 | 188160 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DL | NP201DL | np20 1dl | np201dl | Newport | Casnewydd | Caerleon Road STW | 2927 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331196 | 188049 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DP | NP201DP | np20 1dp | np201dp | Newport | Casnewydd | Caerleon Road STW | 2964 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331195 | 187979 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DQ | NP201DQ | np20 1dq | np201dq | Newport | Casnewydd | Caerleon Road STW | 2968 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331158 | 188033 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DR | NP201DR | np20 1dr | np201dr | Newport | Casnewydd | Caerleon Road STW | 2878 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331258 | 188042 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DS | NP201DS | np20 1ds | np201ds | Newport | Casnewydd | Caerleon Road STW | 2879 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331319 | 187943 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DT | NP201DT | np20 1dt | np201dt | Newport | Casnewydd | Caerleon Road STW | 2963 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331344 | 187761 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DU | NP201DU | np20 1du | np201du | Newport | Casnewydd | Caerleon Road STW | 2898 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331244 | 188026 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DW | NP201DW | np20 1dw | np201dw | Newport | Casnewydd | Caerleon Road STW | 2963 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331140 | 188075 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DX | NP201DX | np20 1dx | np201dx | Newport | Casnewydd | Caerleon Road STW | 2970 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331138 | 188065 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DY | NP201DY | np20 1dy | np201dy | Newport | Casnewydd | Caerleon Road STW | 2937 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331136 | 188137 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1DZ | NP201DZ | np20 1dz | np201dz | Newport | Casnewydd | Caerleon Road STW | 2942 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331119 | 188158 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EA | NP201EA | np20 1ea | np201ea | Newport | Casnewydd | Caerleon Road STW | 2865 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331259 | 188066 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EB | NP201EB | np20 1eb | np201eb | Newport | Casnewydd | Caerleon Road STW | 2983 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331281 | 187815 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1ED | NP201ED | np20 1ed | np201ed | Newport | Casnewydd | Caerleon Road STW | 2951 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331298 | 187846 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EE | NP201EE | np20 1ee | np201ee | Newport | Casnewydd | Caerleon Road STW | 2938 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331413 | 187713 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EF | NP201EF | np20 1ef | np201ef | Newport | Casnewydd | Caerleon Road STW | 2915 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331446 | 187708 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EG | NP201EG | np20 1eg | np201eg | Newport | Casnewydd | Caerleon Road STW | 2932 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331486 | 187632 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EH | NP201EH | np20 1eh | np201eh | Newport | Casnewydd | Caerleon Road STW | 2904 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331530 | 187624 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EJ | NP201EJ | np20 1ej | np201ej | Newport | Casnewydd | Caerleon Road STW | 2867 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331494 | 187724 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EL | NP201EL | np20 1el | np201el | Newport | Casnewydd | Caerleon Road STW | 2893 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331515 | 187658 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EN | NP201EN | np20 1en | np201en | Newport | Casnewydd | Caerleon Road STW | 3039 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331430 | 187533 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EP | NP201EP | np20 1ep | np201ep | Newport | Casnewydd | Caerleon Road STW | 2967 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331440 | 187633 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EQ | NP201EQ | np20 1eq | np201eq | Newport | Casnewydd | Caerleon Road STW | 2854 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331473 | 187772 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1ER | NP201ER | np20 1er | np201er | Newport | Casnewydd | Caerleon Road STW | 2804 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331509 | 187807 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1ES | NP201ES | np20 1es | np201es | Newport | Casnewydd | Caerleon Road STW | 2829 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331483 | 187799 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1ET | NP201ET | np20 1et | np201et | Newport | Casnewydd | Caerleon Road STW | 3002 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331388 | 187641 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EU | NP201EU | np20 1eu | np201eu | Newport | Casnewydd | Caerleon Road STW | 2868 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331432 | 187803 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EW | NP201EW | np20 1ew | np201ew | Newport | Casnewydd | Caerleon Road STW | 3022 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331294 | 187729 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EX | NP201EX | np20 1ex | np201ex | Newport | Casnewydd | Caerleon Road STW | 2977 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331345 | 187737 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1EZ | NP201EZ | np20 1ez | np201ez | Newport | Casnewydd | Caerleon Road STW | 3039 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331416 | 187550 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1FA | NP201FA | np20 1fa | np201fa | Newport | Casnewydd | Caerleon Road STW | 2891 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331206 | 188104 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1FB | NP201FB | np20 1fb | np201fb | Newport | Casnewydd | Caerleon Road STW | 2918 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331034 | 188393 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1FQ | NP201FQ | np20 1fq | np201fq | Newport | Casnewydd | Caerleon Road STW | 2905 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331067 | 188349 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1FS | NP201FS | np20 1fs | np201fs | Newport | Casnewydd | Caerleon Road STW | 2935 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331050 | 188314 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1FU | NP201FU | np20 1fu | np201fu | Newport | Casnewydd | Caerleon Road STW | 2946 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331052 | 188284 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1FW | NP201FW | np20 1fw | np201fw | Newport | Casnewydd | Caerleon Road STW | 2962 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331026 | 188302 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1FX | NP201FX | np20 1fx | np201fx | Newport | Casnewydd | Caerleon Road STW | 2959 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331054 | 188248 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1FZ | NP201FZ | np20 1fz | np201fz | Newport | Casnewydd | Caerleon Road STW | 2977 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331037 | 188242 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1GA | NP201GA | np20 1ga | np201ga | Newport | Casnewydd | Caerleon Road STW | 3001 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330994 | 188278 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1GB | NP201GB | np20 1gb | np201gb | Newport | Casnewydd | Caerleon Road STW | 2992 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330994 | 188299 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1GD | NP201GD | np20 1gd | np201gd | Newport | Casnewydd | Caerleon Road STW | 3019 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330987 | 188249 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1GF | NP201GF | np20 1gf | np201gf | Newport | Casnewydd | Caerleon Road STW | 3019 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331006 | 188211 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1GG | NP201GG | np20 1gg | np201gg | Newport | Casnewydd | Caerleon Road STW | 3036 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331010 | 188163 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1GH | NP201GH | np20 1gh | np201gh | Newport | Casnewydd | Caerleon Road STW | 2987 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331052 | 188189 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1GL | NP201GL | np20 1gl | np201gl | Newport | Casnewydd | Caerleon Road STW | 2963 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331066 | 188214 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1GN | NP201GN | np20 1gn | np201gn | Newport | Casnewydd | Caerleon Road STW | 2977 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331053 | 188210 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1GP | NP201GP | np20 1gp | np201gp | Newport | Casnewydd | Caerleon Road STW | 2989 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331048 | 188193 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1GY | NP201GY | np20 1gy | np201gy | Newport | Casnewydd | Caerleon Road STW | 2950 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331093 | 188191 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1HA | NP201HA | np20 1ha | np201ha | Newport | Casnewydd | Caerleon Road STW | 2891 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331156 | 188196 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1HB | NP201HB | np20 1hb | np201hb | Newport | Casnewydd | Caerleon Road STW | 2960 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331095 | 188165 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1HD | NP201HD | np20 1hd | np201hd | Newport | Casnewydd | Caerleon Road STW | 2989 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331069 | 188152 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1HE | NP201HE | np20 1he | np201he | Newport | Casnewydd | Caerleon Road STW | 2980 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331106 | 188101 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1HF | NP201HF | np20 1hf | np201hf | Newport | Casnewydd | Caerleon Road STW | 2975 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331142 | 188047 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1HG | NP201HG | np20 1hg | np201hg | Newport | Casnewydd | Caerleon Road STW | 2795 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331272 | 188184 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1HJ | NP201HJ | np20 1hj | np201hj | Newport | Casnewydd | Caerleon Road STW | 2989 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331151 | 188004 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1HP | NP201HP | np20 1hp | np201hp | Newport | Casnewydd | Caerleon Road STW | 2995 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331183 | 187940 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1HR | NP201HR | np20 1hr | np201hr | Newport | Casnewydd | Caerleon Road STW | 2992 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331208 | 187907 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1HS | NP201HS | np20 1hs | np201hs | Newport | Casnewydd | Caerleon Road STW | 2992 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331197 | 187924 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1HY | NP201HY | np20 1hy | np201hy | Newport | Casnewydd | Caerleon Road STW | 2990 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331347 | 187713 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1HZ | NP201HZ | np20 1hz | np201hz | Newport | Casnewydd | Caerleon Road STW | 2974 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331228 | 187909 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JB | NP201JB | np20 1jb | np201jb | Newport | Casnewydd | Caerleon Road STW | 3049 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331018 | 188120 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JD | NP201JD | np20 1jd | np201jd | Newport | Casnewydd | Caerleon Road STW | 3073 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331019 | 188066 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JE | NP201JE | np20 1je | np201je | Newport | Casnewydd | Caerleon Road STW | 3083 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331017 | 188049 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JF | NP201JF | np20 1jf | np201jf | Newport | Casnewydd | Caerleon Road STW | 3139 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330993 | 187977 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JG | NP201JG | np20 1jg | np201jg | Newport | Casnewydd | Caerleon Road STW | 3148 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331008 | 187934 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JH | NP201JH | np20 1jh | np201jh | Newport | Casnewydd | Caerleon Road STW | 3132 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331043 | 187906 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JJ | NP201JJ | np20 1jj | np201jj | Newport | Casnewydd | Caerleon Road STW | 3051 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331048 | 188060 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JL | NP201JL | np20 1jl | np201jl | Newport | Casnewydd | Caerleon Road STW | 3029 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331044 | 188114 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JN | NP201JN | np20 1jn | np201jn | Newport | Casnewydd | Caerleon Road STW | 3019 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331081 | 188066 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JQ | NP201JQ | np20 1jq | np201jq | Newport | Casnewydd | Caerleon Road STW | 3032 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331121 | 187970 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JR | NP201JR | np20 1jr | np201jr | Newport | Casnewydd | Caerleon Road STW | 3073 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331138 | 187866 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JS | NP201JS | np20 1js | np201js | Newport | Casnewydd | Caerleon Road STW | 3283 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330969 | 187741 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JT | NP201JT | np20 1jt | np201jt | Newport | Casnewydd | Caerleon Road STW | 3113 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331082 | 187880 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JU | NP201JU | np20 1ju | np201ju | Newport | Casnewydd | Caerleon Road STW | 3118 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331089 | 187859 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JW | NP201JW | np20 1jw | np201jw | Newport | Casnewydd | Caerleon Road STW | 3111 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331117 | 187829 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JX | NP201JX | np20 1jx | np201jx | Newport | Casnewydd | Caerleon Road STW | 3184 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330990 | 187894 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JY | NP201JY | np20 1jy | np201jy | Newport | Casnewydd | Caerleon Road STW | 3227 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330962 | 187856 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1JZ | NP201JZ | np20 1jz | np201jz | Newport | Casnewydd | Caerleon Road STW | 3160 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330965 | 187984 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LA | NP201LA | np20 1la | np201la | Newport | Casnewydd | Caerleon Road STW | 3113 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330984 | 188048 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LB | NP201LB | np20 1lb | np201lb | Newport | Casnewydd | Caerleon Road STW | 3223 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330907 | 187959 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LD | NP201LD | np20 1ld | np201ld | Newport | Casnewydd | Caerleon Road STW | 3159 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330982 | 187957 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LE | NP201LE | np20 1le | np201le | Newport | Casnewydd | Caerleon Road STW | 3060 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331109 | 187936 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LF | NP201LF | np20 1lf | np201lf | Newport | Casnewydd | Caerleon Road STW | 3135 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331078 | 187845 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LN | NP201LN | np20 1ln | np201ln | Newport | Casnewydd | Caerleon Road STW | 3051 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331181 | 187841 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LP | NP201LP | np20 1lp | np201lp | Newport | Casnewydd | Caerleon Road STW | 3019 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331220 | 187840 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LQ | NP201LQ | np20 1lq | np201lq | Newport | Casnewydd | Caerleon Road STW | 3034 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331248 | 187772 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LR | NP201LR | np20 1lr | np201lr | Newport | Casnewydd | Caerleon Road STW | 3051 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331291 | 187685 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LS | NP201LS | np20 1ls | np201ls | Newport | Casnewydd | Caerleon Road STW | 3081 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331331 | 187586 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LT | NP201LT | np20 1lt | np201lt | Newport | Casnewydd | Caerleon Road STW | 3163 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331255 | 187550 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LU | NP201LU | np20 1lu | np201lu | Newport | Casnewydd | Caerleon Road STW | 3124 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331307 | 187547 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LW | NP201LW | np20 1lw | np201lw | Newport | Casnewydd | Caerleon Road STW | 3081 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331276 | 187655 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LX | NP201LX | np20 1lx | np201lx | Newport | Casnewydd | Caerleon Road STW | 3072 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331236 | 187724 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LY | NP201LY | np20 1ly | np201ly | Newport | Casnewydd | Caerleon Road STW | 3064 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331220 | 187760 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1LZ | NP201LZ | np20 1lz | np201lz | Newport | Casnewydd | Caerleon Road STW | 3154 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331113 | 187756 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1NA | NP201NA | np20 1na | np201na | Newport | Casnewydd | Caerleon Road STW | 3082 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331327 | 187590 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1PA | NP201PA | np20 1pa | np201pa | Newport | Casnewydd | Caerleon Road STW | 2968 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331255 | 187879 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1PW | NP201PW | np20 1pw | np201pw | Newport | Casnewydd | Caerleon Road STW | 2971 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331188 | 187978 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1PX | NP201PX | np20 1px | np201px | Newport | Casnewydd | Caerleon Road STW | 2968 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331211 | 187947 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1QY | NP201QY | np20 1qy | np201qy | Newport | Casnewydd | Caerleon Road STW | 3026 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331093 | 188030 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1RL | NP201RL | np20 1rl | np201rl | Newport | Casnewydd | Caerleon Road STW | 2993 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331172 | 187962 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1RN | NP201RN | np20 1rn | np201rn | Newport | Casnewydd | Caerleon Road STW | 2936 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331023 | 188371 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1TE | NP201TE | np20 1te | np201te | Newport | Casnewydd | Caerleon Road STW | 3149 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330928 | 188077 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1TP | NP201TP | np20 1tp | np201tp | Newport | Casnewydd | Caerleon Road STW | 3058 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331056 | 188030 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1TS | NP201TS | np20 1ts | np201ts | Newport | Casnewydd | Caerleon Road STW | 3044 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331146 | 187907 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1UE | NP201UE | np20 1ue | np201ue | Newport | Casnewydd | Caerleon Road STW | 3031 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331133 | 187953 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1WR | NP201WR | np20 1wr | np201wr | Newport | Casnewydd | Caerleon Road STW | 2963 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331344 | 187761 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1WX | NP201WX | np20 1wx | np201wx | Newport | Casnewydd | Caerleon Road STW | 3008 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331197 | 187894 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1YD | NP201YD | np20 1yd | np201yd | Newport | Casnewydd | Caerleon Road STW | 2991 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331155 | 187993 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1YN | NP201YN | np20 1yn | np201yn | Newport | Casnewydd | Caerleon Road STW | 2990 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331001 | 188288 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1YP | NP201YP | np20 1yp | np201yp | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 1ZB | NP201ZB | np20 1zb | np201zb | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AA | NP202AA | np20 2aa | np202aa | Newport | Casnewydd | Caerleon Road STW | 3021 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331469 | 187516 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AB | NP202AB | np20 2ab | np202ab | Newport | Casnewydd | Caerleon Road STW | 2820 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331638 | 187630 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AD | NP202AD | np20 2ad | np202ad | Newport | Casnewydd | Nash STW | 3238 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331538 | 186722 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AE | NP202AE | np20 2ae | np202ae | Newport | Casnewydd | Caerleon Road STW | 2860 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331558 | 187660 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AF | NP202AF | np20 2af | np202af | Newport | Casnewydd | Caerleon Road STW | 2931 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331588 | 187520 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AG | NP202AG | np20 2ag | np202ag | Newport | Casnewydd | Caerleon Road STW | 2927 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331627 | 187486 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AH | NP202AH | np20 2ah | np202ah | Newport | Casnewydd | Caerleon Road STW | 2921 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331757 | 187368 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AJ | NP202AJ | np20 2aj | np202aj | Newport | Casnewydd | Caerleon Road STW | 3020 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331732 | 187258 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AL | NP202AL | np20 2al | np202al | Newport | Casnewydd | Caerleon Road STW | 2788 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331652 | 187661 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AN | NP202AN | np20 2an | np202an | Newport | Casnewydd | Caerleon Road STW | 3160 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331593 | 187194 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AP | NP202AP | np20 2ap | np202ap | Newport | Casnewydd | Caerleon Road STW | 3118 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331615 | 187231 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AQ | NP202AQ | np20 2aq | np202aq | Newport | Casnewydd | Caerleon Road STW | 3175 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331684 | 187095 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AR | NP202AR | np20 2ar | np202ar | Newport | Casnewydd | Caerleon Road STW | 3153 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331564 | 187231 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AS | NP202AS | np20 2as | np202as | Newport | Casnewydd | Caerleon Road STW | 3066 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331635 | 187283 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AT | NP202AT | np20 2at | np202at | Newport | Casnewydd | Caerleon Road STW | 2980 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331720 | 187322 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AU | NP202AU | np20 2au | np202au | Newport | Casnewydd | Caerleon Road STW | 3162 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331526 | 187254 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AW | NP202AW | np20 2aw | np202aw | Newport | Casnewydd | Caerleon Road STW | 3080 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331584 | 187313 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AX | NP202AX | np20 2ax | np202ax | Newport | Casnewydd | Caerleon Road STW | 2966 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331696 | 187363 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AY | NP202AY | np20 2ay | np202ay | Newport | Casnewydd | Caerleon Road STW | 3029 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331642 | 187328 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2AZ | NP202AZ | np20 2az | np202az | Newport | Casnewydd | Caerleon Road STW | 2969 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331561 | 187494 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2BA | NP202BA | np20 2ba | np202ba | Newport | Casnewydd | Caerleon Road STW | 3091 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331444 | 187440 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2BB | NP202BB | np20 2bb | np202bb | Newport | Casnewydd | Caerleon Road STW | 3030 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331487 | 187483 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2BE | NP202BE | np20 2be | np202be | Newport | Casnewydd | Caerleon Road STW | 3123 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331482 | 187354 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2BH | NP202BH | np20 2bh | np202bh | Newport | Casnewydd | Caerleon Road STW | 2955 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331626 | 187446 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2BJ | NP202BJ | np20 2bj | np202bj | Newport | Casnewydd | Caerleon Road STW | 3147 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331420 | 187384 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2BL | NP202BL | np20 2bl | np202bl | Newport | Casnewydd | Caerleon Road STW | 2922 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331806 | 187323 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2BP | NP202BP | np20 2bp | np202bp | Newport | Casnewydd | Caerleon Road STW | 2715 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331734 | 187680 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2BQ | NP202BQ | np20 2bq | np202bq | Newport | Casnewydd | Nash STW | 3197 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331817 | 186857 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2BW | NP202BW | np20 2bw | np202bw | Newport | Casnewydd | Nash STW | 3024 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332117 | 186823 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2BX | NP202BX | np20 2bx | np202bx | Newport | Casnewydd | Nash STW | 2995 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332117 | 186791 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2BY | NP202BY | np20 2by | np202by | Newport | Casnewydd | Nash STW | 3137 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331749 | 186745 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2BZ | NP202BZ | np20 2bz | np202bz | Newport | Casnewydd | Nash STW | 3124 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331836 | 186783 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DA | NP202DA | np20 2da | np202da | Newport | Casnewydd | Nash STW | 3203 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331738 | 186816 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DB | NP202DB | np20 2db | np202db | Newport | Casnewydd | Nash STW | 3290 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331707 | 186899 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DD | NP202DD | np20 2dd | np202dd | Newport | Casnewydd | Caerleon Road STW | 3240 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331807 | 186917 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DE | NP202DE | np20 2de | np202de | Newport | Casnewydd | Caerleon Road STW | 3246 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331766 | 186939 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DF | NP202DF | np20 2df | np202df | Newport | Casnewydd | Nash STW | 3209 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331854 | 186893 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DG | NP202DG | np20 2dg | np202dg | Newport | Casnewydd | Nash STW | 3182 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331883 | 186878 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DH | NP202DH | np20 2dh | np202dh | Newport | Casnewydd | Nash STW | 3127 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331907 | 186829 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DJ | NP202DJ | np20 2dj | np202dj | Newport | Casnewydd | Nash STW | 3092 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331922 | 186797 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DL | NP202DL | np20 2dl | np202dl | Newport | Casnewydd | Nash STW | 3240 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331773 | 186881 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DN | NP202DN | np20 2dn | np202dn | Newport | Casnewydd | Nash STW | 3180 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331904 | 186888 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DP | NP202DP | np20 2dp | np202dp | Newport | Casnewydd | Caerleon Road STW | 3244 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331729 | 186970 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DQ | NP202DQ | np20 2dq | np202dq | Newport | Casnewydd | Caerleon Road STW | 3194 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331757 | 187012 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DR | NP202DR | np20 2dr | np202dr | Newport | Casnewydd | Caerleon Road STW | 3225 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331712 | 187008 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DS | NP202DS | np20 2ds | np202ds | Newport | Casnewydd | Nash STW | 3022 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 331256 | 186186 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DT | NP202DT | np20 2dt | np202dt | Newport | Casnewydd | Caerleon Road STW | 3304 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331589 | 187006 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DU | NP202DU | np20 2du | np202du | Newport | Casnewydd | Caerleon Road STW | 3152 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331843 | 186999 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DW | NP202DW | np20 2dw | np202dw | Newport | Casnewydd | Caerleon Road STW | 2827 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331769 | 187486 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DX | NP202DX | np20 2dx | np202dx | Newport | Casnewydd | Caerleon Road STW | 3223 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331619 | 187088 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DY | NP202DY | np20 2dy | np202dy | Newport | Casnewydd | Caerleon Road STW | 2981 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331709 | 187331 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2DZ | NP202DZ | np20 2dz | np202dz | Newport | Casnewydd | Caerleon Road STW | 2740 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331797 | 187580 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EA | NP202EA | np20 2ea | np202ea | Newport | Casnewydd | Caerleon Road STW | 3167 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331272 | 187523 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EB | NP202EB | np20 2eb | np202eb | Newport | Casnewydd | Caerleon Road STW | 3249 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331216 | 187461 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2ED | NP202ED | np20 2ed | np202ed | Newport | Casnewydd | Caerleon Road STW | 3210 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331273 | 187454 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EE | NP202EE | np20 2ee | np202ee | Newport | Casnewydd | Caerleon Road STW | 3318 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331172 | 187406 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EF | NP202EF | np20 2ef | np202ef | Newport | Casnewydd | Caerleon Road STW | 3406 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331091 | 187367 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EG | NP202EG | np20 2eg | np202eg | Newport | Casnewydd | Caerleon Road STW | 3366 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331170 | 187335 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EH | NP202EH | np20 2eh | np202eh | Newport | Casnewydd | Caerleon Road STW | 3461 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331128 | 187238 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EJ | NP202EJ | np20 2ej | np202ej | Newport | Casnewydd | Caerleon Road STW | 3411 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331210 | 187222 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EL | NP202EL | np20 2el | np202el | Newport | Casnewydd | Caerleon Road STW | 3523 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331105 | 187171 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EQ | NP202EQ | np20 2eq | np202eq | Newport | Casnewydd | Caerleon Road STW | 3559 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331091 | 187133 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2ER | NP202ER | np20 2er | np202er | Newport | Casnewydd | Caerleon Road STW | 3462 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331250 | 187106 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2ES | NP202ES | np20 2es | np202es | Newport | Casnewydd | Caerleon Road STW | 3449 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331231 | 187144 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2ET | NP202ET | np20 2et | np202et | Newport | Casnewydd | Caerleon Road STW | 3506 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331195 | 187100 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EU | NP202EU | np20 2eu | np202eu | Newport | Casnewydd | Caerleon Road STW | 3599 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331097 | 187067 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EW | NP202EW | np20 2ew | np202ew | Newport | Casnewydd | Caerleon Road STW | 3555 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331182 | 187043 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EX | NP202EX | np20 2ex | np202ex | Newport | Casnewydd | Caerleon Road STW | 3368 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331505 | 186995 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EY | NP202EY | np20 2ey | np202ey | Newport | Casnewydd | Caerleon Road STW | 3298 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331257 | 187338 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2EZ | NP202EZ | np20 2ez | np202ez | Newport | Casnewydd | Caerleon Road STW | 3210 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331223 | 187514 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FA | NP202FA | np20 2fa | np202fa | Newport | Casnewydd | Caerleon Road STW | 3224 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331366 | 187328 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FB | NP202FB | np20 2fb | np202fb | Newport | Casnewydd | Caerleon Road STW | 3220 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331345 | 187358 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FD | NP202FD | np20 2fd | np202fd | Newport | Casnewydd | Caerleon Road STW | 3347 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331159 | 187377 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FE | NP202FE | np20 2fe | np202fe | Newport | Casnewydd | Caerleon Road STW | 3174 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331277 | 187506 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FF | NP202FF | np20 2ff | np202ff | Newport | Casnewydd | Caerleon Road STW | 3357 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331154 | 187367 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FG | NP202FG | np20 2fg | np202fg | Newport | Casnewydd | Caerleon Road STW | 3459 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331442 | 186929 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FH | NP202FH | np20 2fh | np202fh | Newport | Casnewydd | Caerleon Road STW | 2865 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332158 | 187130 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FJ | NP202FJ | np20 2fj | np202fj | Newport | Casnewydd | Caerleon Road STW | 2914 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332240 | 187021 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FL | NP202FL | np20 2fl | np202fl | Newport | Casnewydd | Caerleon Road STW | 2889 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332192 | 187079 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FN | NP202FN | np20 2fn | np202fn | Newport | Casnewydd | Caerleon Road STW | 2974 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332304 | 186916 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FP | NP202FP | np20 2fp | np202fp | Newport | Casnewydd | Caerleon Road STW | 2936 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332351 | 186934 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FR | NP202FR | np20 2fr | np202fr | Newport | Casnewydd | Caerleon Road STW | 2911 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332138 | 187087 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FT | NP202FT | np20 2ft | np202ft | Newport | Casnewydd | Caerleon Road STW | 3616 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331161 | 186977 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FW | NP202FW | np20 2fw | np202fw | Newport | Casnewydd | Caerleon Road STW | 2819 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331907 | 187372 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FX | NP202FX | np20 2fx | np202fx | Newport | Casnewydd | Caerleon Road STW | 2772 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331923 | 187420 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FY | NP202FY | np20 2fy | np202fy | Newport | Casnewydd | Nash STW | 2956 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331944 | 186652 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2FZ | NP202FZ | np20 2fz | np202fz | Newport | Casnewydd | Caerleon Road STW | 2915 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332021 | 187162 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GA | NP202GA | np20 2ga | np202ga | Newport | Casnewydd | Caerleon Road STW | 2853 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332129 | 187163 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GD | NP202GD | np20 2gd | np202gd | Newport | Casnewydd | Caerleon Road STW | 2892 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331669 | 187493 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GE | NP202GE | np20 2ge | np202ge | Newport | Casnewydd | Caerleon Road STW | 2816 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 331746 | 187523 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GF | NP202GF | np20 2gf | np202gf | Newport | Casnewydd | Caerleon Road STW | 2901 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332322 | 186989 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GG | NP202GG | np20 2gg | np202gg | Newport | Casnewydd | Caerleon Road STW | 3391 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331530 | 186942 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GH | NP202GH | np20 2gh | np202gh | Newport | Casnewydd | Nash STW | 3431 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331380 | 186845 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GJ | NP202GJ | np20 2gj | np202gj | Newport | Casnewydd | Nash STW | 3387 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331508 | 186883 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GL | NP202GL | np20 2gl | np202gl | Newport | Casnewydd | Nash STW | 3312 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331587 | 186847 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GN | NP202GN | np20 2gn | np202gn | Newport | Casnewydd | Nash STW | 3318 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331541 | 186822 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GQ | NP202GQ | np20 2gq | np202gq | Newport | Casnewydd | Nash STW | 3426 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331455 | 186894 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GR | NP202GR | np20 2gr | np202gr | Newport | Casnewydd | Caerleon Road STW | 2985 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332262 | 186926 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GS | NP202GS | np20 2gs | np202gs | Newport | Casnewydd | Caerleon Road STW | 2963 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332171 | 187005 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GT | NP202GT | np20 2gt | np202gt | Newport | Casnewydd | Caerleon Road STW | 2946 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332080 | 187084 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GW | NP202GW | np20 2gw | np202gw | Newport | Casnewydd | Nash STW | 3285 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331624 | 186839 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GX | NP202GX | np20 2gx | np202gx | Newport | Casnewydd | Nash STW | 3268 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331654 | 186839 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GY | NP202GY | np20 2gy | np202gy | Newport | Casnewydd | Nash STW | 3176 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331594 | 186686 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2GZ | NP202GZ | np20 2gz | np202gz | Newport | Casnewydd | Nash STW | 3230 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331519 | 186698 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HA | NP202HA | np20 2ha | np202ha | Newport | Casnewydd | Nash STW | 3181 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331482 | 186608 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HB | NP202HB | np20 2hb | np202hb | Newport | Casnewydd | Nash STW | 3212 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331407 | 186587 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HD | NP202HD | np20 2hd | np202hd | Newport | Casnewydd | Nash STW | 3189 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331350 | 186509 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HF | NP202HF | np20 2hf | np202hf | Newport | Casnewydd | Nash STW | 3142 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 331274 | 186375 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HG | NP202HG | np20 2hg | np202hg | Newport | Casnewydd | Caerleon Road STW | 2831 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331944 | 187327 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HJ | NP202HJ | np20 2hj | np202hj | Newport | Casnewydd | Caerleon Road STW | 2831 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331971 | 187305 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HL | NP202HL | np20 2hl | np202hl | Newport | Casnewydd | Nash STW | 3020 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 331358 | 186286 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HN | NP202HN | np20 2hn | np202hn | Newport | Casnewydd | Caerleon Road STW | 2839 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331995 | 187276 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HP | NP202HP | np20 2hp | np202hp | Newport | Casnewydd | Nash STW | 2958 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 331428 | 186267 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HQ | NP202HQ | np20 2hq | np202hq | Newport | Casnewydd | Nash STW | 3082 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 331419 | 186427 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HR | NP202HR | np20 2hr | np202hr | Newport | Casnewydd | Nash STW | 3083 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 331344 | 186360 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HS | NP202HS | np20 2hs | np202hs | Newport | Casnewydd | Nash STW | 3115 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 331412 | 186465 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HT | NP202HT | np20 2ht | np202ht | Newport | Casnewydd | Nash STW | 3137 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 331328 | 186419 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HU | NP202HU | np20 2hu | np202hu | Newport | Casnewydd | Nash STW | 3178 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331578 | 186677 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HW | NP202HW | np20 2hw | np202hw | Newport | Casnewydd | Caerleon Road STW | 3318 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331292 | 187270 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HX | NP202HX | np20 2hx | np202hx | Newport | Casnewydd | Nash STW | 2959 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 331389 | 186232 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HY | NP202HY | np20 2hy | np202hy | Newport | Casnewydd | Nash STW | 2963 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 331464 | 186308 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2HZ | NP202HZ | np20 2hz | np202hz | Newport | Casnewydd | Caerleon Road STW | 3087 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332023 | 186952 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JA | NP202JA | np20 2ja | np202ja | Newport | Casnewydd | Caerleon Road STW | 2919 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332093 | 187108 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JB | NP202JB | np20 2jb | np202jb | Newport | Casnewydd | Nash STW | 3143 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331563 | 186622 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JD | NP202JD | np20 2jd | np202jd | Newport | Casnewydd | Nash STW | 3075 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331561 | 186535 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JE | NP202JE | np20 2je | np202je | Newport | Casnewydd | Nash STW | 3088 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 331492 | 186496 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JF | NP202JF | np20 2jf | np202jf | Newport | Casnewydd | Nash STW | 3006 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 331469 | 186370 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JG | NP202JG | np20 2jg | np202jg | Newport | Casnewydd | Nash STW | 2892 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 331517 | 186260 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JH | NP202JH | np20 2jh | np202jh | Newport | Casnewydd | Nash STW | 2866 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 331506 | 186215 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JJ | NP202JJ | np20 2jj | np202jj | Newport | Casnewydd | Nash STW | 3109 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331583 | 186595 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JL | NP202JL | np20 2jl | np202jl | Newport | Casnewydd | Nash STW | 3055 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 331537 | 186490 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JN | NP202JN | np20 2jn | np202jn | Newport | Casnewydd | Nash STW | 3102 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331654 | 186638 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JP | NP202JP | np20 2jp | np202jp | Newport | Casnewydd | Nash STW | 2986 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 331554 | 186415 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JQ | NP202JQ | np20 2jq | np202jq | Newport | Casnewydd | Nash STW | 3055 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331715 | 186623 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JR | NP202JR | np20 2jr | np202jr | Newport | Casnewydd | Nash STW | 2931 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 331727 | 186480 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JS | NP202JS | np20 2js | np202js | Newport | Casnewydd | Nash STW | 2864 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 331609 | 186302 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JT | NP202JT | np20 2jt | np202jt | Newport | Casnewydd | Nash STW | 2943 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 331540 | 186348 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JU | NP202JU | np20 2ju | np202ju | Newport | Casnewydd | Nash STW | 2843 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 331589 | 186258 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JW | NP202JW | np20 2jw | np202jw | Newport | Casnewydd | Nash STW | 3158 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331647 | 186701 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JX | NP202JX | np20 2jx | np202jx | Newport | Casnewydd | Caerleon Road STW | 2915 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332077 | 187123 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JY | NP202JY | np20 2jy | np202jy | Newport | Casnewydd | Nash STW | 2796 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 331674 | 186268 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2JZ | NP202JZ | np20 2jz | np202jz | Newport | Casnewydd | Nash STW | 3228 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331458 | 186649 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2LA | NP202LA | np20 2la | np202la | Newport | Casnewydd | Nash STW | 3273 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331544 | 186769 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2LD | NP202LD | np20 2ld | np202ld | Newport | Casnewydd | Nash STW | 3226 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331547 | 186713 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2LG | NP202LG | np20 2lg | np202lg | Newport | Casnewydd | Caerleon Road STW | 2896 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332271 | 187024 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2LH | NP202LH | np20 2lh | np202lh | Newport | Casnewydd | Caerleon Road STW | 2917 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332250 | 187012 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2LJ | NP202LJ | np20 2lj | np202lj | Newport | Casnewydd | Caerleon Road STW | 2906 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332292 | 187000 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2LN | NP202LN | np20 2ln | np202ln | Newport | Casnewydd | Caerleon Road STW | 2845 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332056 | 187223 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2LQ | NP202LQ | np20 2lq | np202lq | Newport | Casnewydd | Nash STW | 3347 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331403 | 186756 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2LR | NP202LR | np20 2lr | np202lr | Newport | Casnewydd | Caerleon Road STW | 2896 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 332028 | 187181 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2LT | NP202LT | np20 2lt | np202lt | Newport | Casnewydd | Nash STW | 3301 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331467 | 186748 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2LU | NP202LU | np20 2lu | np202lu | Newport | Casnewydd | Nash STW | 3313 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331409 | 186718 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2LX | NP202LX | np20 2lx | np202lx | Newport | Casnewydd | Nash STW | 3203 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331363 | 186538 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2LY | NP202LY | np20 2ly | np202ly | Newport | Casnewydd | Nash STW | 3261 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331291 | 186553 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2NA | NP202NA | np20 2na | np202na | Newport | Casnewydd | Nash STW | 3325 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331358 | 186693 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2NP | NP202NP | np20 2np | np202np | Newport | Casnewydd | Nash STW | 2506 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 331632 | 185834 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2NQ | NP202NQ | np20 2nq | np202nq | Newport | Casnewydd | Nash STW | 1928 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 331760 | 185037 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2NU | NP202NU | np20 2nu | np202nu | Newport | Casnewydd | Caerleon Road STW | 3564 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331102 | 187113 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2NX | NP202NX | np20 2nx | np202nx | Newport | Casnewydd | Nash STW | 3201 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331437 | 186598 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2PA | NP202PA | np20 2pa | np202pa | Newport | Casnewydd | Caerleon Road STW | 3111 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331372 | 187491 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2PB | NP202PB | np20 2pb | np202pb | Newport | Casnewydd | Caerleon Road STW | 3171 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331446 | 187321 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2PD | NP202PD | np20 2pd | np202pd | Newport | Casnewydd | Caerleon Road STW | 3166 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331471 | 187303 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2PE | NP202PE | np20 2pe | np202pe | Newport | Casnewydd | Caerleon Road STW | 3214 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331490 | 187217 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2PF | NP202PF | np20 2pf | np202pf | Newport | Casnewydd | Caerleon Road STW | 3275 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331553 | 187076 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2PG | NP202PG | np20 2pg | np202pg | Newport | Casnewydd | Caerleon Road STW | 3338 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331607 | 186948 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2PH | NP202PH | np20 2ph | np202ph | Newport | Casnewydd | Caerleon Road STW | 3362 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331586 | 186933 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2PJ | NP202PJ | np20 2pj | np202pj | Newport | Casnewydd | Caerleon Road STW | 3299 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331522 | 187072 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2PL | NP202PL | np20 2pl | np202pl | Newport | Casnewydd | Caerleon Road STW | 3247 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331473 | 187188 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2PN | NP202PN | np20 2pn | np202pn | Newport | Casnewydd | Caerleon Road STW | 3197 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331419 | 187312 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2PP | NP202PP | np20 2pp | np202pp | Newport | Casnewydd | Caerleon Road STW | 3157 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331370 | 187424 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2PS | NP202PS | np20 2ps | np202ps | Newport | Casnewydd | Caerleon Road STW | 3157 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331458 | 187329 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2QF | NP202QF | np20 2qf | np202qf | Newport | Casnewydd | Caerleon Road STW | 3348 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331522 | 187006 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2QG | NP202QG | np20 2qg | np202qg | Newport | Casnewydd | Caerleon Road STW | 3440 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331400 | 186991 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2QH | NP202QH | np20 2qh | np202qh | Newport | Casnewydd | Caerleon Road STW | 3361 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331204 | 187304 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RA | NP202RA | np20 2ra | np202ra | Newport | Casnewydd | Caerleon Road STW | 3396 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331288 | 187161 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RB | NP202RB | np20 2rb | np202rb | Newport | Casnewydd | Caerleon Road STW | 3354 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331317 | 187192 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RD | NP202RD | np20 2rd | np202rd | Newport | Casnewydd | Caerleon Road STW | 3272 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331386 | 187239 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RE | NP202RE | np20 2re | np202re | Newport | Casnewydd | Caerleon Road STW | 3288 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331400 | 187201 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RF | NP202RF | np20 2rf | np202rf | Newport | Casnewydd | Caerleon Road STW | 3304 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331416 | 187163 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RG | NP202RG | np20 2rg | np202rg | Newport | Casnewydd | Caerleon Road STW | 3312 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331432 | 187137 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RH | NP202RH | np20 2rh | np202rh | Newport | Casnewydd | Caerleon Road STW | 3327 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331417 | 187130 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RJ | NP202RJ | np20 2rj | np202rj | Newport | Casnewydd | Caerleon Road STW | 3359 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331376 | 187125 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RL | NP202RL | np20 2rl | np202rl | Newport | Casnewydd | Caerleon Road STW | 3367 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331343 | 187147 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RN | NP202RN | np20 2rn | np202rn | Newport | Casnewydd | Caerleon Road STW | 3382 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331366 | 187104 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RP | NP202RP | np20 2rp | np202rp | Newport | Casnewydd | Caerleon Road STW | 3422 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331319 | 187094 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RQ | NP202RQ | np20 2rq | np202rq | Newport | Casnewydd | Caerleon Road STW | 3416 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331366 | 187056 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RR | NP202RR | np20 2rr | np202rr | Newport | Casnewydd | Caerleon Road STW | 3361 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331416 | 187085 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RS | NP202RS | np20 2rs | np202rs | Newport | Casnewydd | Caerleon Road STW | 3359 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331458 | 187048 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RT | NP202RT | np20 2rt | np202rt | Newport | Casnewydd | Caerleon Road STW | 3372 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331473 | 187017 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RU | NP202RU | np20 2ru | np202ru | Newport | Casnewydd | Caerleon Road STW | 3332 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331444 | 187098 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RY | NP202RY | np20 2ry | np202ry | Newport | Casnewydd | Nash STW | 3205 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331366 | 186543 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2RZ | NP202RZ | np20 2rz | np202rz | Newport | Casnewydd | Nash STW | 2153 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 331556 | 185132 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2TJ | NP202TJ | np20 2tj | np202tj | Newport | Casnewydd | Caerleon Road STW | 3119 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331680 | 187172 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2TX | NP202TX | np20 2tx | np202tx | Newport | Casnewydd | Nash STW | 3027 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331994 | 186763 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2UP | NP202UP | np20 2up | np202up | Newport | Casnewydd | Caerleon Road STW | 3164 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331609 | 187174 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2US | NP202US | np20 2us | np202us | Newport | Casnewydd | Nash STW | 2907 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 331647 | 186389 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2UW | NP202UW | np20 2uw | np202uw | Newport | Casnewydd | Nash STW | 2202 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 331845 | 185616 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2WE | NP202WE | np20 2we | np202we | Newport | Casnewydd | Nash STW | 1545 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 331908 | 184193 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2XJ | NP202XJ | np20 2xj | np202xj | Newport | Casnewydd | Caerleon Road STW | 3273 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 331660 | 186988 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 2YB | NP202YB | np20 2yb | np202yb | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 3QN | NP203QN | np20 3qn | np203qn | Newport | Casnewydd | Caerleon Road STW | 3391 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 331186 | 187279 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 3SE | NP203SE | np20 3se | np203se | Newport | Casnewydd | Caerleon Road STW | 5389 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 328635 | 187752 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4AB | NP204AB | np20 4ab | np204ab | Newport | Casnewydd | Caerleon Road STW | 3035 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330983 | 188222 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4AD | NP204AD | np20 4ad | np204ad | Newport | Casnewydd | Caerleon Road STW | 3058 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330955 | 188226 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4AF | NP204AF | np20 4af | np204af | Newport | Casnewydd | Caerleon Road STW | 4046 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330064 | 187801 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4AG | NP204AG | np20 4ag | np204ag | Newport | Casnewydd | Caerleon Road STW | 3146 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330870 | 188200 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4AL | NP204AL | np20 4al | np204al | Newport | Casnewydd | Caerleon Road STW | 3095 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330969 | 188115 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4AN | NP204AN | np20 4an | np204an | Newport | Casnewydd | Caerleon Road STW | 3193 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330864 | 188104 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4AQ | NP204AQ | np20 4aq | np204aq | Newport | Casnewydd | Caerleon Road STW | 3104 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330940 | 188151 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4AT | NP204AT | np20 4at | np204at | Newport | Casnewydd | Caerleon Road STW | 3219 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330812 | 188153 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4AU | NP204AU | np20 4au | np204au | Newport | Casnewydd | Caerleon Road STW | 3152 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330885 | 188154 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4AX | NP204AX | np20 4ax | np204ax | Newport | Casnewydd | Caerleon Road STW | 3050 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330916 | 188332 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BG | NP204BG | np20 4bg | np204bg | Newport | Casnewydd | Caerleon Road STW | 3251 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330806 | 188092 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BH | NP204BH | np20 4bh | np204bh | Newport | Casnewydd | Caerleon Road STW | 3292 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330764 | 188084 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BL | NP204BL | np20 4bl | np204bl | Newport | Casnewydd | Caerleon Road STW | 3224 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330822 | 188119 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BN | NP204BN | np20 4bn | np204bn | Newport | Casnewydd | Caerleon Road STW | 3235 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330831 | 188077 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BP | NP204BP | np20 4bp | np204bp | Newport | Casnewydd | Caerleon Road STW | 3217 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330867 | 188046 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BQ | NP204BQ | np20 4bq | np204bq | Newport | Casnewydd | Caerleon Road STW | 3588 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330535 | 187880 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BR | NP204BR | np20 4br | np204br | Newport | Casnewydd | Caerleon Road STW | 3312 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330758 | 188051 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BS | NP204BS | np20 4bs | np204bs | Newport | Casnewydd | Caerleon Road STW | 3394 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330698 | 187988 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BT | NP204BT | np20 4bt | np204bt | Newport | Casnewydd | Caerleon Road STW | 3444 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330630 | 188012 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BU | NP204BU | np20 4bu | np204bu | Newport | Casnewydd | Caerleon Road STW | 3457 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330609 | 188025 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BW | NP204BW | np20 4bw | np204bw | Newport | Casnewydd | Caerleon Road STW | 3497 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330585 | 187983 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BX | NP204BX | np20 4bx | np204bx | Newport | Casnewydd | Caerleon Road STW | 3558 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330560 | 187898 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BY | NP204BY | np20 4by | np204by | Newport | Casnewydd | Caerleon Road STW | 3582 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330564 | 187839 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4BZ | NP204BZ | np20 4bz | np204bz | Newport | Casnewydd | Caerleon Road STW | 3545 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330594 | 187861 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DA | NP204DA | np20 4da | np204da | Newport | Casnewydd | Caerleon Road STW | 3410 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330722 | 187907 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DB | NP204DB | np20 4db | np204db | Newport | Casnewydd | Caerleon Road STW | 3318 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330773 | 188007 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DD | NP204DD | np20 4dd | np204dd | Newport | Casnewydd | Caerleon Road STW | 3286 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330828 | 187973 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DE | NP204DE | np20 4de | np204de | Newport | Casnewydd | Caerleon Road STW | 3325 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330805 | 187933 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DF | NP204DF | np20 4df | np204df | Newport | Casnewydd | Caerleon Road STW | 3371 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330793 | 187860 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DG | NP204DG | np20 4dg | np204dg | Newport | Casnewydd | Caerleon Road STW | 3322 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330864 | 187836 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DH | NP204DH | np20 4dh | np204dh | Newport | Casnewydd | Caerleon Road STW | 3317 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330849 | 187871 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DJ | NP204DJ | np20 4dj | np204dj | Newport | Casnewydd | Caerleon Road STW | 3223 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330898 | 187976 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DL | NP204DL | np20 4dl | np204dl | Newport | Casnewydd | Caerleon Road STW | 3293 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330875 | 187874 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DP | NP204DP | np20 4dp | np204dp | Newport | Casnewydd | Caerleon Road STW | 3243 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330939 | 187863 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DT | NP204DT | np20 4dt | np204dt | Newport | Casnewydd | Caerleon Road STW | 3300 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331004 | 187657 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DU | NP204DU | np20 4du | np204du | Newport | Casnewydd | Caerleon Road STW | 3265 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331013 | 187707 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DW | NP204DW | np20 4dw | np204dw | Newport | Casnewydd | Caerleon Road STW | 3242 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330999 | 187770 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DX | NP204DX | np20 4dx | np204dx | Newport | Casnewydd | Caerleon Road STW | 3187 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331033 | 187818 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DY | NP204DY | np20 4dy | np204dy | Newport | Casnewydd | Caerleon Road STW | 3311 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330961 | 187701 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4DZ | NP204DZ | np20 4dz | np204dz | Newport | Casnewydd | Caerleon Road STW | 3239 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331032 | 187724 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EA | NP204EA | np20 4ea | np204ea | Newport | Casnewydd | Caerleon Road STW | 3356 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330997 | 187570 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EB | NP204EB | np20 4eb | np204eb | Newport | Casnewydd | Caerleon Road STW | 3390 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330984 | 187531 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4ED | NP204ED | np20 4ed | np204ed | Newport | Casnewydd | Caerleon Road STW | 3500 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330825 | 187565 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EE | NP204EE | np20 4ee | np204ee | Newport | Casnewydd | Caerleon Road STW | 3486 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330850 | 187553 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EG | NP204EG | np20 4eg | np204eg | Newport | Casnewydd | Caerleon Road STW | 3429 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330998 | 187447 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EH | NP204EH | np20 4eh | np204eh | Newport | Casnewydd | Caerleon Road STW | 3262 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331155 | 187516 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EJ | NP204EJ | np20 4ej | np204ej | Newport | Casnewydd | Caerleon Road STW | 3124 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331238 | 187634 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EL | NP204EL | np20 4el | np204el | Newport | Casnewydd | Caerleon Road STW | 3219 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331132 | 187618 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EN | NP204EN | np20 4en | np204en | Newport | Casnewydd | Caerleon Road STW | 3193 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331112 | 187690 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EP | NP204EP | np20 4ep | np204ep | Newport | Casnewydd | Caerleon Road STW | 3128 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331164 | 187728 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EQ | NP204EQ | np20 4eq | np204eq | Newport | Casnewydd | Caerleon Road STW | 3196 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331093 | 187711 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4ER | NP204ER | np20 4er | np204er | Newport | Casnewydd | Caerleon Road STW | 3467 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330891 | 187527 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EU | NP204EU | np20 4eu | np204eu | Newport | Casnewydd | Caerleon Road STW | 3382 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330862 | 187724 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EW | NP204EW | np20 4ew | np204ew | Newport | Casnewydd | Caerleon Road STW | 3489 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330796 | 187628 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4EX | NP204EX | np20 4ex | np204ex | Newport | Casnewydd | Caerleon Road STW | 3429 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330828 | 187689 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4FX | NP204FX | np20 4fx | np204fx | Newport | Casnewydd | Caerleon Road STW | 3703 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330504 | 187697 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4GD | NP204GD | np20 4gd | np204gd | Newport | Casnewydd | Caerleon Road STW | 3616 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330596 | 187711 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4GE | NP204GE | np20 4ge | np204ge | Newport | Casnewydd | Caerleon Road STW | 3537 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330630 | 187812 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4GF | NP204GF | np20 4gf | np204gf | Newport | Casnewydd | Caerleon Road STW | 3655 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330504 | 187795 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4GG | NP204GG | np20 4gg | np204gg | Newport | Casnewydd | Caerleon Road STW | 3504 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330687 | 187777 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4GH | NP204GH | np20 4gh | np204gh | Newport | Casnewydd | Caerleon Road STW | 3505 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330703 | 187748 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4GJ | NP204GJ | np20 4gj | np204gj | Newport | Casnewydd | Caerleon Road STW | 3352 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330852 | 187798 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4GL | NP204GL | np20 4gl | np204gl | Newport | Casnewydd | Caerleon Road STW | 3355 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330860 | 187778 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4GN | NP204GN | np20 4gn | np204gn | Newport | Casnewydd | Caerleon Road STW | 3440 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330777 | 187751 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4GP | NP204GP | np20 4gp | np204gp | Newport | Casnewydd | Caerleon Road STW | 3524 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330714 | 187694 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4GQ | NP204GQ | np20 4gq | np204gq | Newport | Casnewydd | Caerleon Road STW | 3512 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330750 | 187658 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4HG | NP204HG | np20 4hg | np204hg | Newport | Casnewydd | Caerleon Road STW | 3867 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330310 | 187709 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4HH | NP204HH | np20 4hh | np204hh | Newport | Casnewydd | Caerleon Road STW | 3765 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330406 | 187745 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4HJ | NP204HJ | np20 4hj | np204hj | Newport | Casnewydd | Caerleon Road STW | 3612 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330478 | 187941 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4HL | NP204HL | np20 4hl | np204hl | Newport | Casnewydd | Caerleon Road STW | 3569 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330521 | 187951 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4HY | NP204HY | np20 4hy | np204hy | Newport | Casnewydd | Caerleon Road STW | 4287 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329844 | 187701 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4HZ | NP204HZ | np20 4hz | np204hz | Newport | Casnewydd | Caerleon Road STW | 4292 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329825 | 187731 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JD | NP204JD | np20 4jd | np204jd | Newport | Casnewydd | Caerleon Road STW | 4250 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329804 | 187882 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JF | NP204JF | np20 4jf | np204jf | Newport | Casnewydd | Caerleon Road STW | 4320 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329771 | 187783 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JG | NP204JG | np20 4jg | np204jg | Newport | Casnewydd | Caerleon Road STW | 4290 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329804 | 187782 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JH | NP204JH | np20 4jh | np204jh | Newport | Casnewydd | Caerleon Road STW | 4253 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329817 | 187844 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JQ | NP204JQ | np20 4jq | np204jq | Newport | Casnewydd | Caerleon Road STW | 4135 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329998 | 187733 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JR | NP204JR | np20 4jr | np204jr | Newport | Casnewydd | Caerleon Road STW | 3609 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330453 | 188000 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JS | NP204JS | np20 4js | np204js | Newport | Casnewydd | Caerleon Road STW | 3737 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330326 | 187968 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JT | NP204JT | np20 4jt | np204jt | Newport | Casnewydd | Caerleon Road STW | 3953 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330140 | 187857 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JU | NP204JU | np20 4ju | np204ju | Newport | Casnewydd | Caerleon Road STW | 3930 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330179 | 187829 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JW | NP204JW | np20 4jw | np204jw | Newport | Casnewydd | Caerleon Road STW | 4097 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330070 | 187673 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JX | NP204JX | np20 4jx | np204jx | Newport | Casnewydd | Caerleon Road STW | 4040 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330103 | 187734 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JY | NP204JY | np20 4jy | np204jy | Newport | Casnewydd | Caerleon Road STW | 4076 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330059 | 187742 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4JZ | NP204JZ | np20 4jz | np204jz | Newport | Casnewydd | Caerleon Road STW | 3951 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330210 | 187720 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LA | NP204LA | np20 4la | np204la | Newport | Casnewydd | Caerleon Road STW | 3968 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330183 | 187734 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LB | NP204LB | np20 4lb | np204lb | Newport | Casnewydd | Caerleon Road STW | 3798 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330339 | 187802 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LD | NP204LD | np20 4ld | np204ld | Newport | Casnewydd | Caerleon Road STW | 3755 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330342 | 187894 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LN | NP204LN | np20 4ln | np204ln | Newport | Casnewydd | Caerleon Road STW | 4184 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329923 | 187777 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LP | NP204LP | np20 4lp | np204lp | Newport | Casnewydd | Caerleon Road STW | 4119 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329970 | 187829 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LQ | NP204LQ | np20 4lq | np204lq | Newport | Casnewydd | Caerleon Road STW | 4172 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329900 | 187857 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LR | NP204LR | np20 4lr | np204lr | Newport | Casnewydd | Caerleon Road STW | 4138 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329932 | 187868 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LS | NP204LS | np20 4ls | np204ls | Newport | Casnewydd | Caerleon Road STW | 4063 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329982 | 187940 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LT | NP204LT | np20 4lt | np204lt | Newport | Casnewydd | Caerleon Road STW | 4142 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329904 | 187922 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LU | NP204LU | np20 4lu | np204lu | Newport | Casnewydd | Caerleon Road STW | 4213 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329845 | 187880 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LW | NP204LW | np20 4lw | np204lw | Newport | Casnewydd | Caerleon Road STW | 3991 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330044 | 187980 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LX | NP204LX | np20 4lx | np204lx | Newport | Casnewydd | Caerleon Road STW | 3954 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330110 | 187921 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LY | NP204LY | np20 4ly | np204ly | Newport | Casnewydd | Caerleon Road STW | 3712 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330306 | 188075 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4LZ | NP204LZ | np20 4lz | np204lz | Newport | Casnewydd | Caerleon Road STW | 3709 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330328 | 188033 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NA | NP204NA | np20 4na | np204na | Newport | Casnewydd | Caerleon Road STW | 3684 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330284 | 188205 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NB | NP204NB | np20 4nb | np204nb | Newport | Casnewydd | Caerleon Road STW | 3788 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330228 | 188065 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4ND | NP204ND | np20 4nd | np204nd | Newport | Casnewydd | Caerleon Road STW | 3806 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330198 | 188090 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NE | NP204NE | np20 4ne | np204ne | Newport | Casnewydd | Caerleon Road STW | 3885 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330120 | 188073 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NF | NP204NF | np20 4nf | np204nf | Newport | Casnewydd | Caerleon Road STW | 3963 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330037 | 188071 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NG | NP204NG | np20 4ng | np204ng | Newport | Casnewydd | Caerleon Road STW | 4079 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329934 | 188016 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NH | NP204NH | np20 4nh | np204nh | Newport | Casnewydd | Caerleon Road STW | 4213 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329795 | 188003 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NJ | NP204NJ | np20 4nj | np204nj | Newport | Casnewydd | Caerleon Road STW | 3936 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330107 | 187972 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NL | NP204NL | np20 4nl | np204nl | Newport | Casnewydd | Caerleon Road STW | 4011 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329978 | 188090 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NN | NP204NN | np20 4nn | np204nn | Newport | Casnewydd | Caerleon Road STW | 3292 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330685 | 188259 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NT | NP204NT | np20 4nt | np204nt | Newport | Casnewydd | Caerleon Road STW | 3148 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330797 | 188364 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NU | NP204NU | np20 4nu | np204nu | Newport | Casnewydd | Caerleon Road STW | 3133 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330818 | 188351 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NW | NP204NW | np20 4nw | np204nw | Newport | Casnewydd | Caerleon Road STW | 3228 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330731 | 188313 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NX | NP204NX | np20 4nx | np204nx | Newport | Casnewydd | Caerleon Road STW | 3437 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330581 | 188132 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NY | NP204NY | np20 4ny | np204ny | Newport | Casnewydd | Caerleon Road STW | 3396 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330658 | 188065 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4NZ | NP204NZ | np20 4nz | np204nz | Newport | Casnewydd | Caerleon Road STW | 3449 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330595 | 188073 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4PA | NP204PA | np20 4pa | np204pa | Newport | Casnewydd | Caerleon Road STW | 3482 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330544 | 188105 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4PB | NP204PB | np20 4pb | np204pb | Newport | Casnewydd | Caerleon Road STW | 3534 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330496 | 188085 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4PD | NP204PD | np20 4pd | np204pd | Newport | Casnewydd | Caerleon Road STW | 3467 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330543 | 188144 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4PE | NP204PE | np20 4pe | np204pe | Newport | Casnewydd | Caerleon Road STW | 3385 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330583 | 188262 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4PF | NP204PF | np20 4pf | np204pf | Newport | Casnewydd | Caerleon Road STW | 3328 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330633 | 188289 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4PG | NP204PG | np20 4pg | np204pg | Newport | Casnewydd | Caerleon Road STW | 3197 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330734 | 188392 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4PH | NP204PH | np20 4ph | np204ph | Newport | Casnewydd | Caerleon Road STW | 3411 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330516 | 188363 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4PJ | NP204PJ | np20 4pj | np204pj | Newport | Casnewydd | Caerleon Road STW | 3388 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330525 | 188406 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4PL | NP204PL | np20 4pl | np204pl | Newport | Casnewydd | Caerleon Road STW | 3212 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330702 | 188434 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4PQ | NP204PQ | np20 4pq | np204pq | Newport | Casnewydd | Caerleon Road STW | 3408 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330531 | 188331 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4PR | NP204PR | np20 4pr | np204pr | Newport | Casnewydd | Caerleon Road STW | 3507 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330475 | 188204 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4RS | NP204RS | np20 4rs | np204rs | Newport | Casnewydd | Caerleon Road STW | 2979 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331143 | 188038 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4SF | NP204SF | np20 4sf | np204sf | Newport | Casnewydd | Caerleon Road STW | 3229 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330826 | 188100 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4TL | NP204TL | np20 4tl | np204tl | Newport | Casnewydd | Caerleon Road STW | 3942 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330072 | 188039 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4TU | NP204TU | np20 4tu | np204tu | Newport | Casnewydd | Caerleon Road STW | 3497 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330522 | 188119 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4TW | NP204TW | np20 4tw | np204tw | Newport | Casnewydd | Caerleon Road STW | 3469 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330571 | 188078 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4TX | NP204TX | np20 4tx | np204tx | Newport | Casnewydd | Caerleon Road STW | 3369 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330597 | 188269 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4UL | NP204UL | np20 4ul | np204ul | Newport | Casnewydd | Caerleon Road STW | 3220 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330705 | 188402 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4UR | NP204UR | np20 4ur | np204ur | Newport | Casnewydd | Caerleon Road STW | 3556 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330405 | 188247 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4UT | NP204UT | np20 4ut | np204ut | Newport | Casnewydd | Caerleon Road STW | 3047 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 331013 | 188134 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4XN | NP204XN | np20 4xn | np204xn | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 4ZF | NP204ZF | np20 4zf | np204zf | Newport | Casnewydd | Caerleon Road STW | 3556 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330405 | 188247 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5AF | NP205AF | np20 5af | np205af | Newport | Casnewydd | Caerleon Road STW | 5030 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 328972 | 187876 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BA | NP205BA | np20 5ba | np205ba | Newport | Casnewydd | Caerleon Road STW | 3635 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330295 | 188316 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BB | NP205BB | np20 5bb | np205bb | Newport | Casnewydd | Caerleon Road STW | 3815 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330118 | 188277 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BD | NP205BD | np20 5bd | np205bd | Newport | Casnewydd | Caerleon Road STW | 3855 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330099 | 188210 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BE | NP205BE | np20 5be | np205be | Newport | Casnewydd | Caerleon Road STW | 3936 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329986 | 188290 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BG | NP205BG | np20 5bg | np205bg | Newport | Casnewydd | Caerleon Road STW | 4131 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329808 | 188208 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BH | NP205BH | np20 5bh | np205bh | Newport | Casnewydd | Caerleon Road STW | 4054 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329906 | 188159 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BN | NP205BN | np20 5bn | np205bn | Newport | Casnewydd | Caerleon Road STW | 3909 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330065 | 188148 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BP | NP205BP | np20 5bp | np205bp | Newport | Casnewydd | Caerleon Road STW | 3730 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330229 | 188221 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BQ | NP205BQ | np20 5bq | np205bq | Newport | Casnewydd | Caerleon Road STW | 4093 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329812 | 188318 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BR | NP205BR | np20 5br | np205br | Newport | Casnewydd | Caerleon Road STW | 4158 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329825 | 188078 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BS | NP205BS | np20 5bs | np205bs | Newport | Casnewydd | Caerleon Road STW | 4024 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329884 | 188320 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BT | NP205BT | np20 5bt | np205bt | Newport | Casnewydd | Caerleon Road STW | 3927 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330017 | 188228 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BW | NP205BW | np20 5bw | np205bw | Newport | Casnewydd | Caerleon Road STW | 3818 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330148 | 188184 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BX | NP205BX | np20 5bx | np205bx | Newport | Casnewydd | Caerleon Road STW | 3914 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329963 | 188439 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BY | NP205BY | np20 5by | np205by | Newport | Casnewydd | Caerleon Road STW | 3899 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329993 | 188389 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5BZ | NP205BZ | np20 5bz | np205bz | Newport | Casnewydd | Caerleon Road STW | 3925 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329974 | 188362 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5DA | NP205DA | np20 5da | np205da | Newport | Casnewydd | Caerleon Road STW | 3605 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330283 | 188448 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5DB | NP205DB | np20 5db | np205db | Newport | Casnewydd | Caerleon Road STW | 3717 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330131 | 188566 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5DD | NP205DD | np20 5dd | np205dd | Newport | Casnewydd | Caerleon Road STW | 3929 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 329919 | 188541 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5DN | NP205DN | np20 5dn | np205dn | Newport | Casnewydd | Caerleon Road STW | 4125 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 329732 | 188481 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5DP | NP205DP | np20 5dp | np205dp | Newport | Casnewydd | Caerleon Road STW | 3339 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330509 | 188620 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5DQ | NP205DQ | np20 5dq | np205dq | Newport | Casnewydd | Caerleon Road STW | 3513 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330347 | 188552 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5DR | NP205DR | np20 5dr | np205dr | Newport | Casnewydd | Caerleon Road STW | 3417 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330426 | 188624 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5DS | NP205DS | np20 5ds | np205ds | Newport | Casnewydd | Caerleon Road STW | 3391 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330436 | 188688 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5DT | NP205DT | np20 5dt | np205dt | Newport | Casnewydd | Caerleon Road STW | 3368 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330498 | 188553 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5DU | NP205DU | np20 5du | np205du | Newport | Casnewydd | Caerleon Road STW | 3456 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330418 | 188514 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5DX | NP205DX | np20 5dx | np205dx | Newport | Casnewydd | Caerleon Road STW | 3919 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 329906 | 188636 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5DZ | NP205DZ | np20 5dz | np205dz | Newport | Casnewydd | Caerleon Road STW | 3115 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330807 | 188429 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EA | NP205EA | np20 5ea | np205ea | Newport | Casnewydd | Caerleon Road STW | 3553 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330298 | 188579 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EB | NP205EB | np20 5eb | np205eb | Newport | Casnewydd | Caerleon Road STW | 3657 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330158 | 188709 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5ED | NP205ED | np20 5ed | np205ed | Newport | Casnewydd | Caerleon Road STW | 3684 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330157 | 188600 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EE | NP205EE | np20 5ee | np205ee | Newport | Casnewydd | Caerleon Road STW | 3769 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330048 | 188685 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EF | NP205EF | np20 5ef | np205ef | Newport | Casnewydd | Caerleon Road STW | 3783 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330013 | 188781 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EG | NP205EG | np20 5eg | np205eg | Newport | Casnewydd | Caerleon Road STW | 3682 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330102 | 188856 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EH | NP205EH | np20 5eh | np205eh | Newport | Casnewydd | Caerleon Road STW | 3682 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330087 | 188936 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EJ | NP205EJ | np20 5ej | np205ej | Newport | Casnewydd | Caerleon Road STW | 4265 | 1180 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.99 | 11.73 | 12.96 | 329462 | 189314 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EL | NP205EL | np20 5el | np205el | Newport | Casnewydd | Caerleon Road STW | 4821 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 329032 | 188412 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EN | NP205EN | np20 5en | np205en | Newport | Casnewydd | Caerleon Road STW | 3246 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330505 | 189094 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EP | NP205EP | np20 5ep | np205ep | Newport | Casnewydd | Caerleon Road STW | 3302 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330444 | 189127 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EQ | NP205EQ | np20 5eq | np205eq | Newport | Casnewydd | Caerleon Road STW | 3325 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330444 | 188967 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5ER | NP205ER | np20 5er | np205er | Newport | Casnewydd | Caerleon Road STW | 3372 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330407 | 188909 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5ES | NP205ES | np20 5es | np205es | Newport | Casnewydd | Caerleon Road STW | 5281 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 328673 | 187982 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5ET | NP205ET | np20 5et | np205et | Newport | Casnewydd | Caerleon Road STW | 3593 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330191 | 188860 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EU | NP205EU | np20 5eu | np205eu | Newport | Casnewydd | Caerleon Road STW | 3855 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330028 | 188425 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EW | NP205EW | np20 5ew | np205ew | Newport | Casnewydd | Caerleon Road STW | 3811 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330076 | 188419 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EX | NP205EX | np20 5ex | np205ex | Newport | Casnewydd | Caerleon Road STW | 3855 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330028 | 188425 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5EZ | NP205EZ | np20 5ez | np205ez | Newport | Casnewydd | Caerleon Road STW | 3033 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330723 | 189074 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FA | NP205FA | np20 5fa | np205fa | Newport | Casnewydd | Caerleon Road STW | 2904 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330953 | 188652 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FB | NP205FB | np20 5fb | np205fb | Newport | Casnewydd | Caerleon Road STW | 2983 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330891 | 188587 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FD | NP205FD | np20 5fd | np205fd | Newport | Casnewydd | Caerleon Road STW | 3016 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330878 | 188522 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FE | NP205FE | np20 5fe | np205fe | Newport | Casnewydd | Caerleon Road STW | 3005 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330847 | 188652 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FF | NP205FF | np20 5ff | np205ff | Newport | Casnewydd | Caerleon Road STW | 2984 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330829 | 188794 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FG | NP205FG | np20 5fg | np205fg | Newport | Casnewydd | Caerleon Road STW | 3012 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330786 | 188853 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FJ | NP205FJ | np20 5fj | np205fj | Newport | Casnewydd | Caerleon Road STW | 2942 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330815 | 189073 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FL | NP205FL | np20 5fl | np205fl | Newport | Casnewydd | Caerleon Road STW | 2893 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330864 | 189078 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FN | NP205FN | np20 5fn | np205fn | Newport | Casnewydd | Caerleon Road STW | 2998 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330764 | 189038 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FP | NP205FP | np20 5fp | np205fp | Newport | Casnewydd | Caerleon Road STW | 3042 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330725 | 189005 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FQ | NP205FQ | np20 5fq | np205fq | Newport | Casnewydd | Caerleon Road STW | 2994 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330758 | 189099 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FR | NP205FR | np20 5fr | np205fr | Newport | Casnewydd | Caerleon Road STW | 3012 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330732 | 189161 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FS | NP205FS | np20 5fs | np205fs | Newport | Casnewydd | Caerleon Road STW | 3079 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330686 | 189011 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FT | NP205FT | np20 5ft | np205ft | Newport | Casnewydd | Caerleon Road STW | 3125 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330637 | 189026 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FU | NP205FU | np20 5fu | np205fu | Newport | Casnewydd | Caerleon Road STW | 3140 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330616 | 189066 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FW | NP205FW | np20 5fw | np205fw | Newport | Casnewydd | Caerleon Road STW | 3205 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330559 | 189005 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FX | NP205FX | np20 5fx | np205fx | Newport | Casnewydd | Caerleon Road STW | 3212 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330542 | 189073 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FY | NP205FY | np20 5fy | np205fy | Newport | Casnewydd | Caerleon Road STW | 3153 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330593 | 189136 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5FZ | NP205FZ | np20 5fz | np205fz | Newport | Casnewydd | Caerleon Road STW | 3310 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330432 | 189157 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5GA | NP205GA | np20 5ga | np205ga | Newport | Casnewydd | Caerleon Road STW | 3306 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330424 | 189288 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5GB | NP205GB | np20 5gb | np205gb | Newport | Casnewydd | Caerleon Road STW | 3368 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330372 | 189171 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5GD | NP205GD | np20 5gd | np205gd | Newport | Casnewydd | Caerleon Road STW | 3494 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330254 | 189100 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5GE | NP205GE | np20 5ge | np205ge | Newport | Casnewydd | Caerleon Road STW | 3443 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330297 | 189172 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5GF | NP205GF | np20 5gf | np205gf | Newport | Casnewydd | Caerleon Road STW | 3603 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330156 | 189008 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5GG | NP205GG | np20 5gg | np205gg | Newport | Casnewydd | Caerleon Road STW | 3498 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330258 | 189037 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5GJ | NP205GJ | np20 5gj | np205gj | Newport | Casnewydd | Caerleon Road STW | 3060 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330722 | 188924 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5GL | NP205GL | np20 5gl | np205gl | Newport | Casnewydd | Caerleon Road STW | 2993 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330777 | 188993 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5GN | NP205GN | np20 5gn | np205gn | Newport | Casnewydd | Caerleon Road STW | 2853 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330911 | 189037 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5GZ | NP205GZ | np20 5gz | np205gz | Newport | Casnewydd | Caerleon Road STW | 3025 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330914 | 188402 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HA | NP205HA | np20 5ha | np205ha | Newport | Casnewydd | Caerleon Road STW | 2960 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330962 | 188459 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HB | NP205HB | np20 5hb | np205hb | Newport | Casnewydd | Caerleon Road STW | 3112 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330808 | 188435 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HD | NP205HD | np20 5hd | np205hd | Newport | Casnewydd | Caerleon Road STW | 3314 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330584 | 188461 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HE | NP205HE | np20 5he | np205he | Newport | Casnewydd | Caerleon Road STW | 3423 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330476 | 188441 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HF | NP205HF | np20 5hf | np205hf | Newport | Casnewydd | Caerleon Road STW | 3306 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330557 | 188573 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HG | NP205HG | np20 5hg | np205hg | Newport | Casnewydd | Caerleon Road STW | 3207 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330618 | 188721 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HH | NP205HH | np20 5hh | np205hh | Newport | Casnewydd | Caerleon Road STW | 3056 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330770 | 188738 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HJ | NP205HJ | np20 5hj | np205hj | Newport | Casnewydd | Caerleon Road STW | 3053 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330831 | 188546 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HL | NP205HL | np20 5hl | np205hl | Newport | Casnewydd | Caerleon Road STW | 2979 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330928 | 188494 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HN | NP205HN | np20 5hn | np205hn | Newport | Casnewydd | Caerleon Road STW | 2694 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331117 | 188839 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HP | NP205HP | np20 5hp | np205hp | Newport | Casnewydd | Caerleon Road STW | 2690 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331120 | 188844 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HQ | NP205HQ | np20 5hq | np205hq | Newport | Casnewydd | Caerleon Road STW | 2673 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331159 | 188767 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HR | NP205HR | np20 5hr | np205hr | Newport | Casnewydd | Caerleon Road STW | 2649 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331162 | 188844 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HS | NP205HS | np20 5hs | np205hs | Newport | Casnewydd | Caerleon Road STW | 2642 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331159 | 188886 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HT | NP205HT | np20 5ht | np205ht | Newport | Casnewydd | Caerleon Road STW | 2636 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331155 | 188926 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HU | NP205HU | np20 5hu | np205hu | Newport | Casnewydd | Caerleon Road STW | 2671 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331099 | 189019 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HW | NP205HW | np20 5hw | np205hw | Newport | Casnewydd | Caerleon Road STW | 2622 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331152 | 189006 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5HX | NP205HX | np20 5hx | np205hx | Newport | Casnewydd | Caerleon Road STW | 2627 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331146 | 189012 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5JG | NP205JG | np20 5jg | np205jg | Newport | Casnewydd | Caerleon Road STW | 2727 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331037 | 189047 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5JJ | NP205JJ | np20 5jj | np205jj | Newport | Casnewydd | Caerleon Road STW | 2762 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330990 | 189117 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5JL | NP205JL | np20 5jl | np205jl | Newport | Casnewydd | Caerleon Road STW | 2743 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330999 | 189191 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5JN | NP205JN | np20 5jn | np205jn | Newport | Casnewydd | Caerleon Road STW | 2747 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330987 | 189261 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5JT | NP205JT | np20 5jt | np205jt | Newport | Casnewydd | Caerleon Road STW | 2681 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331153 | 188760 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5JU | NP205JU | np20 5ju | np205ju | Newport | Casnewydd | Caerleon Road STW | 2550 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331263 | 188852 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5JZ | NP205JZ | np20 5jz | np205jz | Newport | Casnewydd | Caerleon Road STW | 2569 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331205 | 189010 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LA | NP205LA | np20 5la | np205la | Newport | Casnewydd | Caerleon Road STW | 2590 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331213 | 188883 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LB | NP205LB | np20 5lb | np205lb | Newport | Casnewydd | Caerleon Road STW | 2533 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331258 | 188940 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LD | NP205LD | np20 5ld | np205ld | Newport | Casnewydd | Caerleon Road STW | 2578 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331207 | 188959 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LP | NP205LP | np20 5lp | np205lp | Newport | Casnewydd | Caerleon Road STW | 2665 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 331104 | 190035 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LQ | NP205LQ | np20 5lq | np205lq | Newport | Casnewydd | Caerleon Road STW | 2633 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 331118 | 189924 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LR | NP205LR | np20 5lr | np205lr | Newport | Casnewydd | Caerleon Road STW | 2725 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 331000 | 189676 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LS | NP205LS | np20 5ls | np205ls | Newport | Casnewydd | Caerleon Road STW | 2760 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330961 | 189520 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LT | NP205LT | np20 5lt | np205lt | Newport | Casnewydd | Caerleon Road STW | 2786 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330935 | 189570 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LU | NP205LU | np20 5lu | np205lu | Newport | Casnewydd | Caerleon Road STW | 2817 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330904 | 189540 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LW | NP205LW | np20 5lw | np205lw | Newport | Casnewydd | Caerleon Road STW | 2835 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330886 | 189484 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LX | NP205LX | np20 5lx | np205lx | Newport | Casnewydd | Caerleon Road STW | 2860 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330863 | 189418 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LY | NP205LY | np20 5ly | np205ly | Newport | Casnewydd | Caerleon Road STW | 2870 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330855 | 189383 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5LZ | NP205LZ | np20 5lz | np205lz | Newport | Casnewydd | Caerleon Road STW | 2795 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330928 | 189423 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NA | NP205NA | np20 5na | np205na | Newport | Casnewydd | Caerleon Road STW | 2827 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330902 | 189321 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NB | NP205NB | np20 5nb | np205nb | Newport | Casnewydd | Caerleon Road STW | 2719 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331016 | 189257 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5ND | NP205ND | np20 5nd | np205nd | Newport | Casnewydd | Caerleon Road STW | 2695 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331031 | 189357 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NE | NP205NE | np20 5ne | np205ne | Newport | Casnewydd | Caerleon Road STW | 2637 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331094 | 189296 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NF | NP205NF | np20 5nf | np205nf | Newport | Casnewydd | Caerleon Road STW | 2590 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331150 | 189213 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NG | NP205NG | np20 5ng | np205ng | Newport | Casnewydd | Caerleon Road STW | 2613 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331121 | 189273 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NH | NP205NH | np20 5nh | np205nh | Newport | Casnewydd | Caerleon Road STW | 2426 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331298 | 189411 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NJ | NP205NJ | np20 5nj | np205nj | Newport | Casnewydd | Caerleon Road STW | 2494 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331228 | 189454 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NL | NP205NL | np20 5nl | np205nl | Newport | Casnewydd | Caerleon Road STW | 2454 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 331279 | 189777 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NN | NP205NN | np20 5nn | np205nn | Newport | Casnewydd | Caerleon Road STW | 2631 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331092 | 189436 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NQ | NP205NQ | np20 5nq | np205nq | Newport | Casnewydd | Caerleon Road STW | 2514 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331213 | 189358 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NR | NP205NR | np20 5nr | np205nr | Newport | Casnewydd | Caerleon Road STW | 2409 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331312 | 189481 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NS | NP205NS | np20 5ns | np205ns | Newport | Casnewydd | Caerleon Road STW | 2540 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331181 | 189478 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5NT | NP205NT | np20 5nt | np205nt | Newport | Casnewydd | Caerleon Road STW | 2324 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 331420 | 189857 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PA | NP205PA | np20 5pa | np205pa | Newport | Casnewydd | Caerleon Road STW | 2857 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330880 | 189231 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PB | NP205PB | np20 5pb | np205pb | Newport | Casnewydd | Caerleon Road STW | 2909 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330822 | 189287 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PE | NP205PE | np20 5pe | np205pe | Newport | Casnewydd | Caerleon Road STW | 3049 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330681 | 189296 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PF | NP205PF | np20 5pf | np205pf | Newport | Casnewydd | Caerleon Road STW | 3104 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330620 | 189407 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PG | NP205PG | np20 5pg | np205pg | Newport | Casnewydd | Caerleon Road STW | 3039 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330685 | 189402 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PH | NP205PH | np20 5ph | np205ph | Newport | Casnewydd | Caerleon Road STW | 2993 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330734 | 189334 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PJ | NP205PJ | np20 5pj | np205pj | Newport | Casnewydd | Caerleon Road STW | 2991 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330733 | 189406 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PL | NP205PL | np20 5pl | np205pl | Newport | Casnewydd | Caerleon Road STW | 3041 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330680 | 189530 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PN | NP205PN | np20 5pn | np205pn | Newport | Casnewydd | Caerleon Road STW | 3131 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330591 | 189584 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PP | NP205PP | np20 5pp | np205pp | Newport | Casnewydd | Caerleon Road STW | 3251 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330475 | 189703 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PQ | NP205PQ | np20 5pq | np205pq | Newport | Casnewydd | Caerleon Road STW | 3070 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330653 | 189637 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PR | NP205PR | np20 5pr | np205pr | Newport | Casnewydd | Caerleon Road STW | 3010 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330716 | 189702 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PS | NP205PS | np20 5ps | np205ps | Newport | Casnewydd | Caerleon Road STW | 3484 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330257 | 189897 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PU | NP205PU | np20 5pu | np205pu | Newport | Casnewydd | Caerleon Road STW | 3548 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330192 | 189898 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PW | NP205PW | np20 5pw | np205pw | Newport | Casnewydd | Caerleon Road STW | 3623 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330116 | 189889 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PX | NP205PX | np20 5px | np205px | Newport | Casnewydd | Caerleon Road STW | 3642 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330108 | 189985 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PY | NP205PY | np20 5py | np205py | Newport | Casnewydd | Caerleon Road STW | 3660 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330074 | 189839 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5PZ | NP205PZ | np20 5pz | np205pz | Newport | Casnewydd | Caerleon Road STW | 3668 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330056 | 189675 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QA | NP205QA | np20 5qa | np205qa | Newport | Casnewydd | Caerleon Road STW | 3623 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330106 | 189764 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QB | NP205QB | np20 5qb | np205qb | Newport | Casnewydd | Caerleon Road STW | 3546 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330185 | 189798 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QD | NP205QD | np20 5qd | np205qd | Newport | Casnewydd | Caerleon Road STW | 3010 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330711 | 189532 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QE | NP205QE | np20 5qe | np205qe | Newport | Casnewydd | Caerleon Road STW | 3548 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330176 | 189665 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QF | NP205QF | np20 5qf | np205qf | Newport | Casnewydd | Caerleon Road STW | 2705 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 331046 | 189930 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QG | NP205QG | np20 5qg | np205qg | Newport | Casnewydd | Caerleon Road STW | 2739 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330997 | 189812 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QH | NP205QH | np20 5qh | np205qh | Newport | Casnewydd | Caerleon Road STW | 2890 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330865 | 189969 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QJ | NP205QJ | np20 5qj | np205qj | Newport | Casnewydd | Caerleon Road STW | 2950 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330804 | 189970 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QL | NP205QL | np20 5ql | np205ql | Newport | Casnewydd | Caerleon Road STW | 3100 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330660 | 190021 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QN | NP205QN | np20 5qn | np205qn | Newport | Casnewydd | Caerleon Road STW | 2866 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330883 | 189928 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QP | NP205QP | np20 5qp | np205qp | Newport | Casnewydd | Caerleon Road STW | 2915 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330883 | 190196 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QQ | NP205QQ | np20 5qq | np205qq | Newport | Casnewydd | Caerleon Road STW | 2970 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330813 | 190132 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QR | NP205QR | np20 5qr | np205qr | Newport | Casnewydd | Caerleon Road STW | 3027 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330746 | 190089 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QS | NP205QS | np20 5qs | np205qs | Newport | Casnewydd | Caerleon Road STW | 2938 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330871 | 190243 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QT | NP205QT | np20 5qt | np205qt | Newport | Casnewydd | Caerleon Road STW | 2914 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330930 | 190369 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QU | NP205QU | np20 5qu | np205qu | Newport | Casnewydd | Caerleon Road STW | 2780 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 331003 | 190113 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QW | NP205QW | np20 5qw | np205qw | Newport | Casnewydd | Caerleon Road STW | 2739 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 331016 | 189958 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QX | NP205QX | np20 5qx | np205qx | Newport | Casnewydd | Caerleon Road STW | 2778 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330957 | 189811 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QY | NP205QY | np20 5qy | np205qy | Newport | Casnewydd | Caerleon Road STW | 2819 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330908 | 189709 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5QZ | NP205QZ | np20 5qz | np205qz | Newport | Casnewydd | Caerleon Road STW | 2934 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330790 | 189407 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5RA | NP205RA | np20 5ra | np205ra | Newport | Casnewydd | Caerleon Road STW | 2906 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330815 | 189550 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5RB | NP205RB | np20 5rb | np205rb | Newport | Casnewydd | Caerleon Road STW | 2902 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330824 | 189692 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5RD | NP205RD | np20 5rd | np205rd | Newport | Casnewydd | Caerleon Road STW | 2960 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330761 | 189522 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5RE | NP205RE | np20 5re | np205re | Newport | Casnewydd | Caerleon Road STW | 3005 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330716 | 189582 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5RR | NP205RR | np20 5rr | np205rr | Newport | Casnewydd | Caerleon Road STW | 2552 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331200 | 189132 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5RY | NP205RY | np20 5ry | np205ry | Newport | Casnewydd | Caerleon Road STW | 2787 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330938 | 189687 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5RZ | NP205RZ | np20 5rz | np205rz | Newport | Casnewydd | Caerleon Road STW | 2901 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330822 | 189428 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5WJ | NP205WJ | np20 5wj | np205wj | Newport | Casnewydd | Caerleon Road STW | 3334 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 330592 | 188379 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5XE | NP205XE | np20 5xe | np205xe | Newport | Casnewydd | Caerleon Road STW | 3411 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 330344 | 189054 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5XX | NP205XX | np20 5xx | np205xx | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5YL | NP205YL | np20 5yl | np205yl | Newport | Casnewydd | Caerleon Road STW | 2909 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 330904 | 188806 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 5ZN | NP205ZN | np20 5zn | np205zn | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6AA | NP206AA | np20 6aa | np206aa | Newport | Casnewydd | Caerleon Road STW | 3611 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330183 | 190251 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6AD | NP206AD | np20 6ad | np206ad | Newport | Casnewydd | Caerleon Road STW | 4239 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329875 | 191312 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6EP | NP206EP | np20 6ep | np206ep | Newport | Casnewydd | Caerleon Road STW | 3572 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330249 | 190367 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6EQ | NP206EQ | np20 6eq | np206eq | Newport | Casnewydd | Caerleon Road STW | 3628 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330191 | 190368 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6ER | NP206ER | np20 6er | np206er | Newport | Casnewydd | Caerleon Road STW | 3637 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330203 | 190453 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6ES | NP206ES | np20 6es | np206es | Newport | Casnewydd | Caerleon Road STW | 3571 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330277 | 190473 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6ET | NP206ET | np20 6et | np206et | Newport | Casnewydd | Caerleon Road STW | 3645 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330218 | 190538 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6EU | NP206EU | np20 6eu | np206eu | Newport | Casnewydd | Caerleon Road STW | 3739 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330125 | 190552 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6EW | NP206EW | np20 6ew | np206ew | Newport | Casnewydd | Caerleon Road STW | 3593 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330300 | 190628 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6EX | NP206EX | np20 6ex | np206ex | Newport | Casnewydd | Caerleon Road STW | 3565 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330368 | 190740 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6EY | NP206EY | np20 6ey | np206ey | Newport | Casnewydd | Caerleon Road STW | 3514 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330414 | 190717 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6EZ | NP206EZ | np20 6ez | np206ez | Newport | Casnewydd | Caerleon Road STW | 3523 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330436 | 190801 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FA | NP206FA | np20 6fa | np206fa | Newport | Casnewydd | Caerleon Road STW | 3610 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330333 | 190777 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FB | NP206FB | np20 6fb | np206fb | Newport | Casnewydd | Caerleon Road STW | 3730 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330231 | 190844 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FD | NP206FD | np20 6fd | np206fd | Newport | Casnewydd | Caerleon Road STW | 3738 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330251 | 190919 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FE | NP206FE | np20 6fe | np206fe | Newport | Casnewydd | Caerleon Road STW | 3628 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330350 | 190871 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FF | NP206FF | np20 6ff | np206ff | Newport | Casnewydd | Caerleon Road STW | 3669 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330345 | 190967 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FG | NP206FG | np20 6fg | np206fg | Newport | Casnewydd | Caerleon Road STW | 3620 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330369 | 190897 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FH | NP206FH | np20 6fh | np206fh | Newport | Casnewydd | Caerleon Road STW | 3768 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330254 | 191005 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FJ | NP206FJ | np20 6fj | np206fj | Newport | Casnewydd | Caerleon Road STW | 3723 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330313 | 191027 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FL | NP206FL | np20 6fl | np206fl | Newport | Casnewydd | Caerleon Road STW | 3791 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330219 | 190981 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FN | NP206FN | np20 6fn | np206fn | Newport | Casnewydd | Caerleon Road STW | 3752 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330308 | 191087 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FP | NP206FP | np20 6fp | np206fp | Newport | Casnewydd | Caerleon Road STW | 3823 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330222 | 191070 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FQ | NP206FQ | np20 6fq | np206fq | Newport | Casnewydd | Caerleon Road STW | 3885 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330107 | 190955 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FR | NP206FR | np20 6fr | np206fr | Newport | Casnewydd | Caerleon Road STW | 3918 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330082 | 190982 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FS | NP206FS | np20 6fs | np206fs | Newport | Casnewydd | Caerleon Road STW | 3893 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330081 | 190910 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FT | NP206FT | np20 6ft | np206ft | Newport | Casnewydd | Caerleon Road STW | 3978 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329964 | 190837 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FU | NP206FU | np20 6fu | np206fu | Newport | Casnewydd | Caerleon Road STW | 4093 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329860 | 190886 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FW | NP206FW | np20 6fw | np206fw | Newport | Casnewydd | Caerleon Road STW | 4064 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329896 | 190903 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FX | NP206FX | np20 6fx | np206fx | Newport | Casnewydd | Caerleon Road STW | 4047 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329922 | 190924 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FY | NP206FY | np20 6fy | np206fy | Newport | Casnewydd | Caerleon Road STW | 3981 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329975 | 190875 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6FZ | NP206FZ | np20 6fz | np206fz | Newport | Casnewydd | Caerleon Road STW | 3994 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329998 | 190975 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6GA | NP206GA | np20 6ga | np206ga | Newport | Casnewydd | Caerleon Road STW | 3559 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330326 | 190596 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6GB | NP206GB | np20 6gb | np206gb | Newport | Casnewydd | Caerleon Road STW | 3701 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330248 | 190809 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6GP | NP206GP | np20 6gp | np206gp | Newport | Casnewydd | Caerleon Road STW | 3374 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330361 | 189839 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6GQ | NP206GQ | np20 6gq | np206gq | Newport | Casnewydd | Caerleon Road STW | 3493 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330271 | 190074 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6GR | NP206GR | np20 6gr | np206gr | Newport | Casnewydd | Caerleon Road STW | 3410 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330375 | 190184 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6GS | NP206GS | np20 6gs | np206gs | Newport | Casnewydd | Caerleon Road STW | 3486 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330341 | 190381 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6GT | NP206GT | np20 6gt | np206gt | Newport | Casnewydd | Caerleon Road STW | 3451 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330416 | 190521 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6GU | NP206GU | np20 6gu | np206gu | Newport | Casnewydd | Caerleon Road STW | 3423 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330437 | 190496 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6GW | NP206GW | np20 6gw | np206gw | Newport | Casnewydd | Caerleon Road STW | 3338 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330510 | 190441 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6GX | NP206GX | np20 6gx | np206gx | Newport | Casnewydd | Caerleon Road STW | 3240 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330602 | 190408 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6GY | NP206GY | np20 6gy | np206gy | Newport | Casnewydd | Caerleon Road STW | 3172 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330668 | 190391 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6GZ | NP206GZ | np20 6gz | np206gz | Newport | Casnewydd | Caerleon Road STW | 3369 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330507 | 190539 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6HA | NP206HA | np20 6ha | np206ha | Newport | Casnewydd | Caerleon Road STW | 3246 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330622 | 190494 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6HB | NP206HB | np20 6hb | np206hb | Newport | Casnewydd | Caerleon Road STW | 3378 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330455 | 190393 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6HD | NP206HD | np20 6hd | np206hd | Newport | Casnewydd | Caerleon Road STW | 3239 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330582 | 190329 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6HE | NP206HE | np20 6he | np206he | Newport | Casnewydd | Caerleon Road STW | 3445 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330371 | 190332 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6HF | NP206HF | np20 6hf | np206hf | Newport | Casnewydd | Caerleon Road STW | 3392 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330412 | 190275 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6HG | NP206HG | np20 6hg | np206hg | Newport | Casnewydd | Caerleon Road STW | 3285 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 330520 | 190266 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6HH | NP206HH | np20 6hh | np206hh | Newport | Casnewydd | Caerleon Road STW | 3288 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330489 | 190134 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6HJ | NP206HJ | np20 6hj | np206hj | Newport | Casnewydd | Caerleon Road STW | 3506 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330299 | 190290 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JA | NP206JA | np20 6ja | np206ja | Newport | Casnewydd | Caerleon Road STW | 3587 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330473 | 191051 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JB | NP206JB | np20 6jb | np206jb | Newport | Casnewydd | Caerleon Road STW | 3555 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330510 | 191056 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JD | NP206JD | np20 6jd | np206jd | Newport | Casnewydd | Caerleon Road STW | 3468 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330617 | 191077 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JE | NP206JE | np20 6je | np206je | Newport | Casnewydd | Caerleon Road STW | 3495 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330591 | 191085 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JF | NP206JF | np20 6jf | np206jf | Newport | Casnewydd | Caerleon Road STW | 3419 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330617 | 190962 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JG | NP206JG | np20 6jg | np206jg | Newport | Casnewydd | Caerleon Road STW | 3377 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330679 | 190995 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JH | NP206JH | np20 6jh | np206jh | Newport | Casnewydd | Caerleon Road STW | 3286 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330725 | 190879 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JJ | NP206JJ | np20 6jj | np206jj | Newport | Casnewydd | Caerleon Road STW | 3425 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330592 | 190922 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JL | NP206JL | np20 6jl | np206jl | Newport | Casnewydd | Caerleon Road STW | 3296 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330762 | 190981 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JN | NP206JN | np20 6jn | np206jn | Newport | Casnewydd | Caerleon Road STW | 3389 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330728 | 191120 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JP | NP206JP | np20 6jp | np206jp | Newport | Casnewydd | Caerleon Road STW | 3432 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330677 | 191115 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JQ | NP206JQ | np20 6jq | np206jq | Newport | Casnewydd | Caerleon Road STW | 3462 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330735 | 191281 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JR | NP206JR | np20 6jr | np206jr | Newport | Casnewydd | Caerleon Road STW | 3516 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330664 | 191266 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JS | NP206JS | np20 6js | np206js | Newport | Casnewydd | Caerleon Road STW | 3582 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330567 | 191228 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JT | NP206JT | np20 6jt | np206jt | Newport | Casnewydd | Caerleon Road STW | 3605 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330577 | 191293 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JU | NP206JU | np20 6ju | np206ju | Newport | Casnewydd | Caerleon Road STW | 3610 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330608 | 191357 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JW | NP206JW | np20 6jw | np206jw | Newport | Casnewydd | Caerleon Road STW | 3618 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330659 | 191457 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JX | NP206JX | np20 6jx | np206jx | Newport | Casnewydd | Caerleon Road STW | 3589 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330647 | 191382 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JY | NP206JY | np20 6jy | np206jy | Newport | Casnewydd | Caerleon Road STW | 3684 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330539 | 191386 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6JZ | NP206JZ | np20 6jz | np206jz | Newport | Casnewydd | Caerleon Road STW | 3525 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330600 | 191168 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LA | NP206LA | np20 6la | np206la | Newport | Casnewydd | Caerleon Road STW | 3633 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330520 | 191247 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LB | NP206LB | np20 6lb | np206lb | Newport | Casnewydd | Caerleon Road STW | 3668 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330443 | 191174 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LD | NP206LD | np20 6ld | np206ld | Newport | Casnewydd | Caerleon Road STW | 3776 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330377 | 191284 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LE | NP206LE | np20 6le | np206le | Newport | Casnewydd | Caerleon Road STW | 3821 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330366 | 191357 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LF | NP206LF | np20 6lf | np206lf | Newport | Casnewydd | Caerleon Road STW | 2979 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 331013 | 190770 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LG | NP206LG | np20 6lg | np206lg | Newport | Casnewydd | Caerleon Road STW | 3266 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330928 | 191223 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LH | NP206LH | np20 6lh | np206lh | Newport | Casnewydd | Caerleon Road STW | 3228 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330915 | 191125 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LJ | NP206LJ | np20 6lj | np206lj | Newport | Casnewydd | Caerleon Road STW | 3273 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330847 | 191095 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LL | NP206LL | np20 6ll | np206ll | Newport | Casnewydd | Caerleon Road STW | 3172 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330926 | 191029 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LN | NP206LN | np20 6ln | np206ln | Newport | Casnewydd | Caerleon Road STW | 3080 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 331057 | 191076 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LP | NP206LP | np20 6lp | np206lp | Newport | Casnewydd | Caerleon Road STW | 3087 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330989 | 190966 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LQ | NP206LQ | np20 6lq | np206lq | Newport | Casnewydd | Caerleon Road STW | 3161 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 331013 | 191160 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LR | NP206LR | np20 6lr | np206lr | Newport | Casnewydd | Caerleon Road STW | 3013 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 331048 | 190921 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LS | NP206LS | np20 6ls | np206ls | Newport | Casnewydd | Caerleon Road STW | 3026 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 331019 | 190891 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LT | NP206LT | np20 6lt | np206lt | Newport | Casnewydd | Caerleon Road STW | 3032 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 331000 | 190868 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LU | NP206LU | np20 6lu | np206lu | Newport | Casnewydd | Caerleon Road STW | 3066 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330948 | 190837 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LW | NP206LW | np20 6lw | np206lw | Newport | Casnewydd | Caerleon Road STW | 3022 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 331107 | 191046 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LX | NP206LX | np20 6lx | np206lx | Newport | Casnewydd | Caerleon Road STW | 3872 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330261 | 191268 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6LY | NP206LY | np20 6ly | np206ly | Newport | Casnewydd | Caerleon Road STW | 3830 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330285 | 191222 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NA | NP206NA | np20 6na | np206na | Newport | Casnewydd | Caerleon Road STW | 3622 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330421 | 191022 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NB | NP206NB | np20 6nb | np206nb | Newport | Casnewydd | Caerleon Road STW | 3518 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330503 | 190951 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6ND | NP206ND | np20 6nd | np206nd | Newport | Casnewydd | Caerleon Road STW | 3698 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330368 | 191090 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NE | NP206NE | np20 6ne | np206ne | Newport | Casnewydd | Caerleon Road STW | 3796 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330293 | 191159 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NF | NP206NF | np20 6nf | np206nf | Newport | Casnewydd | Caerleon Road STW | 3870 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330284 | 191307 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NG | NP206NG | np20 6ng | np206ng | Newport | Casnewydd | Caerleon Road STW | 3952 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330223 | 191368 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NH | NP206NH | np20 6nh | np206nh | Newport | Casnewydd | Caerleon Road STW | 3931 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330126 | 191120 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NJ | NP206NJ | np20 6nj | np206nj | Newport | Casnewydd | Caerleon Road STW | 3919 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330169 | 191186 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NL | NP206NL | np20 6nl | np206nl | Newport | Casnewydd | Caerleon Road STW | 4002 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330117 | 191269 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NN | NP206NN | np20 6nn | np206nn | Newport | Casnewydd | Caerleon Road STW | 4041 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330071 | 191264 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NP | NP206NP | np20 6np | np206np | Newport | Casnewydd | Caerleon Road STW | 4076 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330012 | 191220 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NQ | NP206NQ | np20 6nq | np206nq | Newport | Casnewydd | Caerleon Road STW | 4047 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330112 | 191360 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NR | NP206NR | np20 6nr | np206nr | Newport | Casnewydd | Caerleon Road STW | 3972 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330185 | 191339 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NS | NP206NS | np20 6ns | np206ns | Newport | Casnewydd | Caerleon Road STW | 4167 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329990 | 191384 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NT | NP206NT | np20 6nt | np206nt | Newport | Casnewydd | Caerleon Road STW | 4172 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329917 | 191242 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NU | NP206NU | np20 6nu | np206nu | Newport | Casnewydd | Caerleon Road STW | 4188 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329875 | 191187 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NW | NP206NW | np20 6nw | np206nw | Newport | Casnewydd | Caerleon Road STW | 4333 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329733 | 191222 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NX | NP206NX | np20 6nx | np206nx | Newport | Casnewydd | Caerleon Road STW | 4535 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329552 | 191312 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NY | NP206NY | np20 6ny | np206ny | Newport | Casnewydd | Caerleon Road STW | 4357 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329745 | 191311 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6NZ | NP206NZ | np20 6nz | np206nz | Newport | Casnewydd | Caerleon Road STW | 4435 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329685 | 191366 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PA | NP206PA | np20 6pa | np206pa | Newport | Casnewydd | Caerleon Road STW | 4441 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329721 | 191458 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PB | NP206PB | np20 6pb | np206pb | Newport | Casnewydd | Caerleon Road STW | 4386 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329774 | 191441 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PD | NP206PD | np20 6pd | np206pd | Newport | Casnewydd | STW Serving Court Farm Wtw | 4310 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 329845 | 191526 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PE | NP206PE | np20 6pe | np206pe | Newport | Casnewydd | STW Serving Court Farm Wtw | 4307 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329868 | 191487 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PF | NP206PF | np20 6pf | np206pf | Newport | Casnewydd | Caerleon Road STW | 4326 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329808 | 191374 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PG | NP206PG | np20 6pg | np206pg | Newport | Casnewydd | Caerleon Road STW | 4025 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330165 | 191414 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PH | NP206PH | np20 6ph | np206ph | Newport | Casnewydd | Caerleon Road STW | 3906 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330197 | 191214 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PJ | NP206PJ | np20 6pj | np206pj | Newport | Casnewydd | Caerleon Road STW | 3395 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330812 | 191280 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PL | NP206PL | np20 6pl | np206pl | Newport | Casnewydd | Caerleon Road STW | 3329 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330916 | 191323 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PN | NP206PN | np20 6pn | np206pn | Newport | Casnewydd | Caerleon Road STW | 3478 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330833 | 191468 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PP | NP206PP | np20 6pp | np206pp | Newport | Casnewydd | STW Serving Court Farm Wtw | 3489 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 330698 | 191668 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PQ | NP206PQ | np20 6pq | np206pq | Newport | Casnewydd | STW Serving Court Farm Wtw | 3512 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 330730 | 191570 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PR | NP206PR | np20 6pr | np206pr | Newport | Casnewydd | Caerleon Road STW | 3535 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330764 | 191467 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PS | NP206PS | np20 6ps | np206ps | Newport | Casnewydd | Caerleon Road STW | 3682 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330459 | 191238 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PT | NP206PT | np20 6pt | np206pt | Newport | Casnewydd | Caerleon Road STW | 3610 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330480 | 191120 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6PW | NP206PW | np20 6pw | np206pw | Newport | Casnewydd | Caerleon Road STW | 3528 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330451 | 190854 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QA | NP206QA | np20 6qa | np206qa | Newport | Casnewydd | STW Serving Court Farm Wtw | 3973 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330176 | 191618 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QB | NP206QB | np20 6qb | np206qb | Newport | Casnewydd | STW Serving Court Farm Wtw | 4031 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330066 | 191710 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QD | NP206QD | np20 6qd | np206qd | Newport | Casnewydd | STW Serving Court Farm Wtw | 3923 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330258 | 191567 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QE | NP206QE | np20 6qe | np206qe | Newport | Casnewydd | STW Serving Court Farm Wtw | 3879 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330212 | 191758 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QF | NP206QF | np20 6qf | np206qf | Newport | Casnewydd | STW Serving Court Farm Wtw | 3903 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330228 | 191669 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QG | NP206QG | np20 6qg | np206qg | Newport | Casnewydd | STW Serving Court Farm Wtw | 3704 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330426 | 191720 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QH | NP206QH | np20 6qh | np206qh | Newport | Casnewydd | STW Serving Court Farm Wtw | 3816 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330252 | 191822 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QJ | NP206QJ | np20 6qj | np206qj | Newport | Casnewydd | STW Serving Court Farm Wtw | 3749 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330339 | 191793 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QL | NP206QL | np20 6ql | np206ql | Newport | Casnewydd | STW Serving Court Farm Wtw | 3811 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330313 | 191705 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QN | NP206QN | np20 6qn | np206qn | Newport | Casnewydd | STW Serving Court Farm Wtw | 3857 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330342 | 191552 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QP | NP206QP | np20 6qp | np206qp | Newport | Casnewydd | STW Serving Court Farm Wtw | 3714 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330440 | 191670 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QQ | NP206QQ | np20 6qq | np206qq | Newport | Casnewydd | STW Serving Court Farm Wtw | 3649 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 330529 | 191643 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QR | NP206QR | np20 6qr | np206qr | Newport | Casnewydd | STW Serving Court Farm Wtw | 3775 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330436 | 191550 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QS | NP206QS | np20 6qs | np206qs | Newport | Casnewydd | Caerleon Road STW | 3809 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330437 | 191458 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QT | NP206QT | np20 6qt | np206qt | Newport | Casnewydd | Caerleon Road STW | 3908 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330303 | 191423 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QU | NP206QU | np20 6qu | np206qu | Newport | Casnewydd | Caerleon Road STW | 3872 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330360 | 191452 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QW | NP206QW | np20 6qw | np206qw | Newport | Casnewydd | STW Serving Court Farm Wtw | 3993 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330191 | 191545 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QY | NP206QY | np20 6qy | np206qy | Newport | Casnewydd | STW Serving Court Farm Wtw | 3921 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330149 | 191793 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6QZ | NP206QZ | np20 6qz | np206qz | Newport | Casnewydd | STW Serving Court Farm Wtw | 3951 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330261 | 191504 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WA | NP206WA | np20 6wa | np206wa | Newport | Casnewydd | Caerleon Road STW | 3576 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330215 | 190234 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WB | NP206WB | np20 6wb | np206wb | Newport | Casnewydd | Caerleon Road STW | 3510 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330351 | 190509 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WD | NP206WD | np20 6wd | np206wd | Newport | Casnewydd | Caerleon Road STW | 3457 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 330470 | 190705 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WE | NP206WE | np20 6we | np206we | Newport | Casnewydd | Caerleon Road STW | 3420 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330516 | 190723 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WF | NP206WF | np20 6wf | np206wf | Newport | Casnewydd | Caerleon Road STW | 3358 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330553 | 190642 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WG | NP206WG | np20 6wg | np206wg | Newport | Casnewydd | Caerleon Road STW | 3234 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330709 | 190706 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WH | NP206WH | np20 6wh | np206wh | Newport | Casnewydd | Caerleon Road STW | 3423 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330555 | 190831 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WJ | NP206WJ | np20 6wj | np206wj | Newport | Casnewydd | Caerleon Road STW | 3101 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330817 | 190616 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WL | NP206WL | np20 6wl | np206wl | Newport | Casnewydd | Caerleon Road STW | 2964 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330933 | 190537 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WN | NP206WN | np20 6wn | np206wn | Newport | Casnewydd | Caerleon Road STW | 3018 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330924 | 190664 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WP | NP206WP | np20 6wp | np206wp | Newport | Casnewydd | Caerleon Road STW | 3097 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330880 | 190763 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WQ | NP206WQ | np20 6wq | np206wq | Newport | Casnewydd | Caerleon Road STW | 3285 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330686 | 190786 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WR | NP206WR | np20 6wr | np206wr | Newport | Casnewydd | Caerleon Road STW | 3361 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330603 | 190784 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WS | NP206WS | np20 6ws | np206ws | Newport | Casnewydd | Caerleon Road STW | 3200 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330778 | 190785 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WT | NP206WT | np20 6wt | np206wt | Newport | Casnewydd | Caerleon Road STW | 3277 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330720 | 190845 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6WU | NP206WU | np20 6wu | np206wu | Newport | Casnewydd | Caerleon Road STW | 3159 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 330848 | 190843 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6YD | NP206YD | np20 6yd | np206yd | Newport | Casnewydd | Caerleon Road STW | 2879 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 331052 | 190610 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6YE | NP206YE | np20 6ye | np206ye | Newport | Casnewydd | Caerleon Road STW | 2809 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 331070 | 190458 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6YN | NP206YN | np20 6yn | np206yn | Newport | Casnewydd | Caerleon Road STW | 3240 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330488 | 189739 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 6ZE | NP206ZE | np20 6ze | np206ze | Newport | Casnewydd | STW Serving Court Farm Wtw | 3719 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 330516 | 191525 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AA | NP207AA | np20 7aa | np207aa | Newport | Casnewydd | Caerleon Road STW | 5324 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328643 | 191126 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AB | NP207AB | np20 7ab | np207ab | Newport | Casnewydd | Caerleon Road STW | 4131 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 329695 | 190453 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AD | NP207AD | np20 7ad | np207ad | Newport | Casnewydd | Caerleon Road STW | 5306 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328453 | 190158 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AE | NP207AE | np20 7ae | np207ae | Newport | Casnewydd | Caerleon Road STW | 5130 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328862 | 191174 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AF | NP207AF | np20 7af | np207af | Newport | Casnewydd | Caerleon Road STW | 5160 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328806 | 191100 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AG | NP207AG | np20 7ag | np207ag | Newport | Casnewydd | Caerleon Road STW | 5204 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328743 | 191043 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AH | NP207AH | np20 7ah | np207ah | Newport | Casnewydd | Caerleon Road STW | 5309 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328639 | 191063 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AJ | NP207AJ | np20 7aj | np207aj | Newport | Casnewydd | Caerleon Road STW | 5279 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328649 | 190991 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AL | NP207AL | np20 7al | np207al | Newport | Casnewydd | Caerleon Road STW | 5103 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328842 | 191024 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AN | NP207AN | np20 7an | np207an | Newport | Casnewydd | Caerleon Road STW | 5084 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328878 | 191073 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AP | NP207AP | np20 7ap | np207ap | Newport | Casnewydd | Caerleon Road STW | 5357 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328538 | 190880 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AQ | NP207AQ | np20 7aq | np207aq | Newport | Casnewydd | Caerleon Road STW | 5234 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328690 | 190972 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AR | NP207AR | np20 7ar | np207ar | Newport | Casnewydd | Caerleon Road STW | 5128 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328808 | 190996 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AS | NP207AS | np20 7as | np207as | Newport | Casnewydd | Caerleon Road STW | 5287 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328586 | 190786 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AT | NP207AT | np20 7at | np207at | Newport | Casnewydd | Caerleon Road STW | 5112 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328787 | 190865 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AU | NP207AU | np20 7au | np207au | Newport | Casnewydd | Caerleon Road STW | 5182 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328689 | 190763 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AW | NP207AW | np20 7aw | np207aw | Newport | Casnewydd | Caerleon Road STW | 5226 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328677 | 190894 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AX | NP207AX | np20 7ax | np207ax | Newport | Casnewydd | Caerleon Road STW | 5258 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328620 | 190800 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AY | NP207AY | np20 7ay | np207ay | Newport | Casnewydd | Caerleon Road STW | 5186 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328702 | 190832 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7AZ | NP207AZ | np20 7az | np207az | Newport | Casnewydd | Caerleon Road STW | 3670 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 330120 | 190236 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BA | NP207BA | np20 7ba | np207ba | Newport | Casnewydd | Caerleon Road STW | 5404 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328433 | 190640 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BB | NP207BB | np20 7bb | np207bb | Newport | Casnewydd | Caerleon Road STW | 5391 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328438 | 190601 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BD | NP207BD | np20 7bd | np207bd | Newport | Casnewydd | Caerleon Road STW | 5327 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328512 | 190642 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BE | NP207BE | np20 7be | np207be | Newport | Casnewydd | Caerleon Road STW | 5371 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328487 | 190731 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BG | NP207BG | np20 7bg | np207bg | Newport | Casnewydd | Caerleon Road STW | 5438 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328434 | 190799 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BH | NP207BH | np20 7bh | np207bh | Newport | Casnewydd | Caerleon Road STW | 5450 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328431 | 190838 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BJ | NP207BJ | np20 7bj | np207bj | Newport | Casnewydd | Caerleon Road STW | 5382 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328492 | 190799 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BL | NP207BL | np20 7bl | np207bl | Newport | Casnewydd | Caerleon Road STW | 5321 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328540 | 190738 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BN | NP207BN | np20 7bn | np207bn | Newport | Casnewydd | Caerleon Road STW | 5342 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328579 | 190976 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BP | NP207BP | np20 7bp | np207bp | Newport | Casnewydd | Caerleon Road STW | 4294 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 329519 | 190412 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BQ | NP207BQ | np20 7bq | np207bq | Newport | Casnewydd | Caerleon Road STW | 4351 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329471 | 190462 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BR | NP207BR | np20 7br | np207br | Newport | Casnewydd | Caerleon Road STW | 4425 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329384 | 190403 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BS | NP207BS | np20 7bs | np207bs | Newport | Casnewydd | Caerleon Road STW | 4413 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329388 | 190366 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BT | NP207BT | np20 7bt | np207bt | Newport | Casnewydd | Caerleon Road STW | 4532 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329273 | 190395 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BU | NP207BU | np20 7bu | np207bu | Newport | Casnewydd | Caerleon Road STW | 4456 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329336 | 190321 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BW | NP207BW | np20 7bw | np207bw | Newport | Casnewydd | Caerleon Road STW | 4584 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329238 | 190482 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BX | NP207BX | np20 7bx | np207bx | Newport | Casnewydd | Caerleon Road STW | 4635 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329169 | 190400 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BY | NP207BY | np20 7by | np207by | Newport | Casnewydd | Caerleon Road STW | 4677 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329151 | 190521 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7BZ | NP207BZ | np20 7bz | np207bz | Newport | Casnewydd | Caerleon Road STW | 4497 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329338 | 190532 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DA | NP207DA | np20 7da | np207da | Newport | Casnewydd | Caerleon Road STW | 4436 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329397 | 190517 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DB | NP207DB | np20 7db | np207db | Newport | Casnewydd | Caerleon Road STW | 4317 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 329513 | 190491 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DD | NP207DD | np20 7dd | np207dd | Newport | Casnewydd | Caerleon Road STW | 4390 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329478 | 190656 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DE | NP207DE | np20 7de | np207de | Newport | Casnewydd | Caerleon Road STW | 4482 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329384 | 190657 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DF | NP207DF | np20 7df | np207df | Newport | Casnewydd | Caerleon Road STW | 4486 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329403 | 190745 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DG | NP207DG | np20 7dg | np207dg | Newport | Casnewydd | Caerleon Road STW | 4558 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329326 | 190734 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DH | NP207DH | np20 7dh | np207dh | Newport | Casnewydd | Caerleon Road STW | 4588 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329310 | 190790 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DJ | NP207DJ | np20 7dj | np207dj | Newport | Casnewydd | Caerleon Road STW | 4680 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329240 | 190879 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DL | NP207DL | np20 7dl | np207dl | Newport | Casnewydd | Caerleon Road STW | 4820 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329111 | 190935 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DN | NP207DN | np20 7dn | np207dn | Newport | Casnewydd | Caerleon Road STW | 4498 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329413 | 190821 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DP | NP207DP | np20 7dp | np207dp | Newport | Casnewydd | Caerleon Road STW | 4359 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329532 | 190732 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DQ | NP207DQ | np20 7dq | np207dq | Newport | Casnewydd | Caerleon Road STW | 4358 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329546 | 190777 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DR | NP207DR | np20 7dr | np207dr | Newport | Casnewydd | Caerleon Road STW | 4305 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329582 | 190712 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DS | NP207DS | np20 7ds | np207ds | Newport | Casnewydd | Caerleon Road STW | 4277 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329626 | 190761 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DT | NP207DT | np20 7dt | np207dt | Newport | Casnewydd | Caerleon Road STW | 4271 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329604 | 190664 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DU | NP207DU | np20 7du | np207du | Newport | Casnewydd | Caerleon Road STW | 4200 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329695 | 190726 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DW | NP207DW | np20 7dw | np207dw | Newport | Casnewydd | Caerleon Road STW | 4925 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329004 | 190945 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DX | NP207DX | np20 7dx | np207dx | Newport | Casnewydd | Caerleon Road STW | 4843 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329071 | 190880 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DY | NP207DY | np20 7dy | np207dy | Newport | Casnewydd | Caerleon Road STW | 4685 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329223 | 190837 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7DZ | NP207DZ | np20 7dz | np207dz | Newport | Casnewydd | Caerleon Road STW | 5059 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328808 | 190732 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7EA | NP207EA | np20 7ea | np207ea | Newport | Casnewydd | Caerleon Road STW | 4795 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329108 | 190837 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7EB | NP207EB | np20 7eb | np207eb | Newport | Casnewydd | Caerleon Road STW | 4807 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329091 | 190821 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7ED | NP207ED | np20 7ed | np207ed | Newport | Casnewydd | Caerleon Road STW | 4694 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329195 | 190773 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7EE | NP207EE | np20 7ee | np207ee | Newport | Casnewydd | Caerleon Road STW | 4701 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329240 | 190948 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7EF | NP207EF | np20 7ef | np207ef | Newport | Casnewydd | Caerleon Road STW | 4781 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329160 | 190960 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7EG | NP207EG | np20 7eg | np207eg | Newport | Casnewydd | Caerleon Road STW | 4864 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329032 | 190819 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7EH | NP207EH | np20 7eh | np207eh | Newport | Casnewydd | Caerleon Road STW | 4945 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329012 | 191038 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7EJ | NP207EJ | np20 7ej | np207ej | Newport | Casnewydd | Caerleon Road STW | 4788 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329165 | 191001 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7EL | NP207EL | np20 7el | np207el | Newport | Casnewydd | Caerleon Road STW | 4939 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329000 | 190978 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7EN | NP207EN | np20 7en | np207en | Newport | Casnewydd | Caerleon Road STW | 4937 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329011 | 191006 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7EP | NP207EP | np20 7ep | np207ep | Newport | Casnewydd | Caerleon Road STW | 5308 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328586 | 190871 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7EQ | NP207EQ | np20 7eq | np207eq | Newport | Casnewydd | Caerleon Road STW | 4355 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329484 | 190533 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7ER | NP207ER | np20 7er | np207er | Newport | Casnewydd | Caerleon Road STW | 4219 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 329596 | 190415 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7GA | NP207GA | np20 7ga | np207ga | Newport | Casnewydd | Caerleon Road STW | 5038 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328933 | 191094 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7GB | NP207GB | np20 7gb | np207gb | Newport | Casnewydd | Caerleon Road STW | 4146 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 329615 | 190102 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7GG | NP207GG | np20 7gg | np207gg | Newport | Casnewydd | Caerleon Road STW | 4113 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 329671 | 190245 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7GH | NP207GH | np20 7gh | np207gh | Newport | Casnewydd | Caerleon Road STW | 4195 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 329573 | 190152 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7GL | NP207GL | np20 7gl | np207gl | Newport | Casnewydd | Caerleon Road STW | 4111 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 329661 | 190173 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7GN | NP207GN | np20 7gn | np207gn | Newport | Casnewydd | Caerleon Road STW | 4204 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 329591 | 190311 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7GU | NP207GU | np20 7gu | np207gu | Newport | Casnewydd | Caerleon Road STW | 4212 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 329593 | 190365 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7HL | NP207HL | np20 7hl | np207hl | Newport | Casnewydd | Caerleon Road STW | 4768 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329014 | 190284 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7LA | NP207LA | np20 7la | np207la | Newport | Casnewydd | Caerleon Road STW | 5295 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328481 | 190288 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7LN | NP207LN | np20 7ln | np207ln | Newport | Casnewydd | Caerleon Road STW | 4536 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329367 | 190801 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7LP | NP207LP | np20 7lp | np207lp | Newport | Casnewydd | Caerleon Road STW | 4382 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329498 | 190696 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7LQ | NP207LQ | np20 7lq | np207lq | Newport | Casnewydd | Caerleon Road STW | 5214 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328702 | 190939 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7LX | NP207LX | np20 7lx | np207lx | Newport | Casnewydd | Caerleon Road STW | 4249 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329605 | 190582 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7LY | NP207LY | np20 7ly | np207ly | Newport | Casnewydd | Caerleon Road STW | 4294 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329562 | 190598 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RA | NP207RA | np20 7ra | np207ra | Newport | Casnewydd | Caerleon Road STW | 4574 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329396 | 191017 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RB | NP207RB | np20 7rb | np207rb | Newport | Casnewydd | Caerleon Road STW | 4533 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329457 | 191067 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RD | NP207RD | np20 7rd | np207rd | Newport | Casnewydd | Caerleon Road STW | 4723 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329272 | 191112 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RP | NP207RP | np20 7rp | np207rp | Newport | Casnewydd | Caerleon Road STW | 4846 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328958 | 190417 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RQ | NP207RQ | np20 7rq | np207rq | Newport | Casnewydd | Caerleon Road STW | 4695 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329105 | 190382 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RR | NP207RR | np20 7rr | np207rr | Newport | Casnewydd | Caerleon Road STW | 4740 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329052 | 190346 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RS | NP207RS | np20 7rs | np207rs | Newport | Casnewydd | Caerleon Road STW | 4807 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328985 | 190348 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RT | NP207RT | np20 7rt | np207rt | Newport | Casnewydd | Caerleon Road STW | 4922 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328867 | 190343 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RU | NP207RU | np20 7ru | np207ru | Newport | Casnewydd | Caerleon Road STW | 4990 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328794 | 190319 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RW | NP207RW | np20 7rw | np207rw | Newport | Casnewydd | Caerleon Road STW | 4951 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328826 | 190265 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RX | NP207RX | np20 7rx | np207rx | Newport | Casnewydd | Caerleon Road STW | 5155 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328615 | 190236 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RY | NP207RY | np20 7ry | np207ry | Newport | Casnewydd | Caerleon Road STW | 5188 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328590 | 190295 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7RZ | NP207RZ | np20 7rz | np207rz | Newport | Casnewydd | Caerleon Road STW | 5298 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328468 | 190212 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SA | NP207SA | np20 7sa | np207sa | Newport | Casnewydd | Caerleon Road STW | 5333 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328440 | 190269 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SB | NP207SB | np20 7sb | np207sb | Newport | Casnewydd | Caerleon Road STW | 5216 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328573 | 190366 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SD | NP207SD | np20 7sd | np207sd | Newport | Casnewydd | Caerleon Road STW | 5355 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328414 | 190241 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SE | NP207SE | np20 7se | np207se | Newport | Casnewydd | Caerleon Road STW | 5371 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328402 | 190270 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SF | NP207SF | np20 7sf | np207sf | Newport | Casnewydd | Caerleon Road STW | 5413 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328360 | 190275 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SG | NP207SG | np20 7sg | np207sg | Newport | Casnewydd | Caerleon Road STW | 5437 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328346 | 190346 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SH | NP207SH | np20 7sh | np207sh | Newport | Casnewydd | Caerleon Road STW | 5460 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328318 | 190308 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SJ | NP207SJ | np20 7sj | np207sj | Newport | Casnewydd | Caerleon Road STW | 5469 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328317 | 190368 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SL | NP207SL | np20 7sl | np207sl | Newport | Casnewydd | Caerleon Road STW | 5321 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328465 | 190355 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SN | NP207SN | np20 7sn | np207sn | Newport | Casnewydd | Caerleon Road STW | 5295 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328504 | 190433 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SP | NP207SP | np20 7sp | np207sp | Newport | Casnewydd | Caerleon Road STW | 5358 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328440 | 190430 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SQ | NP207SQ | np20 7sq | np207sq | Newport | Casnewydd | Caerleon Road STW | 5370 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328441 | 190506 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SR | NP207SR | np20 7sr | np207sr | Newport | Casnewydd | Caerleon Road STW | 5382 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328407 | 190379 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SS | NP207SS | np20 7ss | np207ss | Newport | Casnewydd | Caerleon Road STW | 5364 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328458 | 190560 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7ST | NP207ST | np20 7st | np207st | Newport | Casnewydd | Caerleon Road STW | 5256 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328590 | 190665 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SU | NP207SU | np20 7su | np207su | Newport | Casnewydd | Caerleon Road STW | 5449 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328367 | 190538 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SW | NP207SW | np20 7sw | np207sw | Newport | Casnewydd | Caerleon Road STW | 5442 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328402 | 190678 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SX | NP207SX | np20 7sx | np207sx | Newport | Casnewydd | Caerleon Road STW | 5455 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328344 | 190446 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SY | NP207SY | np20 7sy | np207sy | Newport | Casnewydd | Caerleon Road STW | 5489 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328329 | 190550 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7SZ | NP207SZ | np20 7sz | np207sz | Newport | Casnewydd | Caerleon Road STW | 5491 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328355 | 190689 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TA | NP207TA | np20 7ta | np207ta | Newport | Casnewydd | Caerleon Road STW | 5551 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328302 | 190731 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TB | NP207TB | np20 7tb | np207tb | Newport | Casnewydd | Caerleon Road STW | 5490 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328383 | 190807 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TD | NP207TD | np20 7td | np207td | Newport | Casnewydd | Caerleon Road STW | 5029 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328889 | 190922 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TH | NP207TH | np20 7th | np207th | Newport | Casnewydd | Caerleon Road STW | 4934 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328964 | 190836 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TL | NP207TL | np20 7tl | np207tl | Newport | Casnewydd | Caerleon Road STW | 4991 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328892 | 190789 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TN | NP207TN | np20 7tn | np207tn | Newport | Casnewydd | Caerleon Road STW | 5060 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328839 | 190859 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TP | NP207TP | np20 7tp | np207tp | Newport | Casnewydd | Caerleon Road STW | 4544 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329298 | 190568 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TQ | NP207TQ | np20 7tq | np207tq | Newport | Casnewydd | Caerleon Road STW | 4590 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329240 | 190521 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TR | NP207TR | np20 7tr | np207tr | Newport | Casnewydd | Caerleon Road STW | 4702 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329154 | 190644 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TS | NP207TS | np20 7ts | np207ts | Newport | Casnewydd | Caerleon Road STW | 4856 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328999 | 190661 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TT | NP207TT | np20 7tt | np207tt | Newport | Casnewydd | Caerleon Road STW | 4993 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328850 | 190624 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TU | NP207TU | np20 7tu | np207tu | Newport | Casnewydd | Caerleon Road STW | 4921 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328915 | 190586 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TW | NP207TW | np20 7tw | np207tw | Newport | Casnewydd | Caerleon Road STW | 5017 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328815 | 190578 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TX | NP207TX | np20 7tx | np207tx | Newport | Casnewydd | Caerleon Road STW | 4847 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328993 | 190596 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TY | NP207TY | np20 7ty | np207ty | Newport | Casnewydd | Caerleon Road STW | 4818 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329014 | 190557 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7TZ | NP207TZ | np20 7tz | np207tz | Newport | Casnewydd | Caerleon Road STW | 4926 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328901 | 190545 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7UA | NP207UA | np20 7ua | np207ua | Newport | Casnewydd | Caerleon Road STW | 4978 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328829 | 190449 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7UB | NP207UB | np20 7ub | np207ub | Newport | Casnewydd | Caerleon Road STW | 5055 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328741 | 190396 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7UD | NP207UD | np20 7ud | np207ud | Newport | Casnewydd | Caerleon Road STW | 4695 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329115 | 190439 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7UE | NP207UE | np20 7ue | np207ue | Newport | Casnewydd | Caerleon Road STW | 4789 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329022 | 190451 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7UF | NP207UF | np20 7uf | np207uf | Newport | Casnewydd | Caerleon Road STW | 4871 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328938 | 190448 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7UG | NP207UG | np20 7ug | np207ug | Newport | Casnewydd | Caerleon Road STW | 5007 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328788 | 190381 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7UH | NP207UH | np20 7uh | np207uh | Newport | Casnewydd | Caerleon Road STW | 4550 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329383 | 190901 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7UJ | NP207UJ | np20 7uj | np207uj | Newport | Casnewydd | Caerleon Road STW | 4673 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 329283 | 190992 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7UL | NP207UL | np20 7ul | np207ul | Newport | Casnewydd | Caerleon Road STW | 4732 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329088 | 190488 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7UN | NP207UN | np20 7un | np207un | Newport | Casnewydd | Caerleon Road STW | 4801 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 329018 | 190491 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7UP | NP207UP | np20 7up | np207up | Newport | Casnewydd | Caerleon Road STW | 4914 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 328898 | 190470 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XA | NP207XA | np20 7xa | np207xa | Newport | Casnewydd | Caerleon Road STW | 5345 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328605 | 191074 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XB | NP207XB | np20 7xb | np207xb | Newport | Casnewydd | Caerleon Road STW | 5411 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328547 | 191111 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XD | NP207XD | np20 7xd | np207xd | Newport | Casnewydd | Caerleon Road STW | 5426 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328515 | 191058 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XE | NP207XE | np20 7xe | np207xe | Newport | Casnewydd | Caerleon Road STW | 5429 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 328550 | 191181 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XF | NP207XF | np20 7xf | np207xf | Newport | Casnewydd | Caerleon Road STW | 5482 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328480 | 191136 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XG | NP207XG | np20 7xg | np207xg | Newport | Casnewydd | Caerleon Road STW | 5505 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328424 | 191024 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XH | NP207XH | np20 7xh | np207xh | Newport | Casnewydd | Caerleon Road STW | 5533 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 328270 | 190475 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XJ | NP207XJ | np20 7xj | np207xj | Newport | Casnewydd | Caerleon Road STW | 5569 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328264 | 190635 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XL | NP207XL | np20 7xl | np207xl | Newport | Casnewydd | Caerleon Road STW | 5613 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328210 | 190591 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XN | NP207XN | np20 7xn | np207xn | Newport | Casnewydd | Caerleon Road STW | 5634 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328183 | 190560 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XP | NP207XP | np20 7xp | np207xp | Newport | Casnewydd | Caerleon Road STW | 5565 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328315 | 190845 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XQ | NP207XQ | np20 7xq | np207xq | Newport | Casnewydd | Caerleon Road STW | 5729 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328149 | 190858 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XR | NP207XR | np20 7xr | np207xr | Newport | Casnewydd | Caerleon Road STW | 5630 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328253 | 190866 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XS | NP207XS | np20 7xs | np207xs | Newport | Casnewydd | Caerleon Road STW | 5546 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328345 | 190889 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XT | NP207XT | np20 7xt | np207xt | Newport | Casnewydd | Caerleon Road STW | 5669 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328215 | 190877 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XU | NP207XU | np20 7xu | np207xu | Newport | Casnewydd | Caerleon Road STW | 5571 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328334 | 190946 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XW | NP207XW | np20 7xw | np207xw | Newport | Casnewydd | Caerleon Road STW | 5606 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328251 | 190754 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XX | NP207XX | np20 7xx | np207xx | Newport | Casnewydd | Caerleon Road STW | 5442 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328475 | 190973 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XY | NP207XY | np20 7xy | np207xy | Newport | Casnewydd | Caerleon Road STW | 5423 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328482 | 190927 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7XZ | NP207XZ | np20 7xz | np207xz | Newport | Casnewydd | Caerleon Road STW | 5441 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 328455 | 190897 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7YA | NP207YA | np20 7ya | np207ya | Newport | Casnewydd | Caerleon Road STW | 4240 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 329595 | 190503 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 7YB | NP207YB | np20 7yb | np207yb | Newport | Casnewydd | Caerleon Road STW | 3975 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 329816 | 190271 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9AR | NP209AR | np20 9ar | np209ar | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9EW | NP209EW | np20 9ew | np209ew | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9HA | NP209HA | np20 9ha | np209ha | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9HP | NP209HP | np20 9hp | np209hp | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9HS | NP209HS | np20 9hs | np209hs | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9HW | NP209HW | np20 9hw | np209hw | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9HZ | NP209HZ | np20 9hz | np209hz | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9LE | NP209LE | np20 9le | np209le | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9LP | NP209LP | np20 9lp | np209lp | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9LR | NP209LR | np20 9lr | np209lr | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9LU | NP209LU | np20 9lu | np209lu | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9LW | NP209LW | np20 9lw | np209lw | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9LX | NP209LX | np20 9lx | np209lx | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9NA | NP209NA | np20 9na | np209na | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9NH | NP209NH | np20 9nh | np209nh | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9NS | NP209NS | np20 9ns | np209ns | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9NY | NP209NY | np20 9ny | np209ny | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9PA | NP209PA | np20 9pa | np209pa | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9PF | NP209PF | np20 9pf | np209pf | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9PP | NP209PP | np20 9pp | np209pp | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9QA | NP209QA | np20 9qa | np209qa | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9QB | NP209QB | np20 9qb | np209qb | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9QY | NP209QY | np20 9qy | np209qy | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9RA | NP209RA | np20 9ra | np209ra | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9RD | NP209RD | np20 9rd | np209rd | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9RG | NP209RG | np20 9rg | np209rg | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9RL | NP209RL | np20 9rl | np209rl | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9RN | NP209RN | np20 9rn | np209rn | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9RW | NP209RW | np20 9rw | np209rw | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9RY | NP209RY | np20 9ry | np209ry | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9SA | NP209SA | np20 9sa | np209sa | Newport | Casnewydd | Caerleon Road STW | 3556 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330405 | 188247 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9SB | NP209SB | np20 9sb | np209sb | Newport | Casnewydd | Caerleon Road STW | 3551 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330415 | 188235 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9SD | NP209SD | np20 9sd | np209sd | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9SF | NP209SF | np20 9sf | np209sf | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9SL | NP209SL | np20 9sl | np209sl | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9SP | NP209SP | np20 9sp | np209sp | Newport | Casnewydd | Caerleon Road STW | 2879 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 331026 | 188518 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP20 9ZZ | NP209ZZ | np20 9zz | np209zz | Newport | Casnewydd | Caerleon Road STW | 3551 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 330415 | 188235 | Newport LPA | SO | River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council
NP23 4AB | NP234AB | np23 4ab | np234ab | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1873 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319055 | 211744 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AD | NP234AD | np23 4ad | np234ad | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1808 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319099 | 211811 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AE | NP234AE | np23 4ae | np234ae | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1878 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319002 | 211885 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AF | NP234AF | np23 4af | np234af | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1856 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319035 | 211852 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AG | NP234AG | np23 4ag | np234ag | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1871 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319033 | 211810 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AH | NP234AH | np23 4ah | np234ah | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2064 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318888 | 211645 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AJ | NP234AJ | np23 4aj | np234aj | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1780 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319156 | 211740 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AL | NP234AL | np23 4al | np234al | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2426 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 318695 | 211213 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AN | NP234AN | np23 4an | np234an | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1810 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319123 | 211742 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AP | NP234AP | np23 4ap | np234ap | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1921 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319054 | 211620 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AQ | NP234AQ | np23 4aq | np234aq | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1871 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319050 | 211763 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AR | NP234AR | np23 4ar | np234ar | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2058 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318907 | 211616 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AS | NP234AS | np23 4as | np234as | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1981 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318956 | 211701 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AT | NP234AT | np23 4at | np234at | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1286 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 319654 | 211836 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AU | NP234AU | np23 4au | np234au | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1341 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 319593 | 211836 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AW | NP234AW | np23 4aw | np234aw | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1903 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319049 | 211676 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AX | NP234AX | np23 4ax | np234ax | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1410 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 319530 | 211808 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4AZ | NP234AZ | np23 4az | np234az | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1770 | 1521 | Over1500 | 3.04 | 2.23 | 1.63 | 28.35 | 15.12 | 16.71 | 319548 | 211164 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4BA | NP234BA | np23 4ba | np234ba | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2688 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 318550 | 210948 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4BB | NP234BB | np23 4bb | np234bb | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2710 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 318543 | 210919 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4BE | NP234BE | np23 4be | np234be | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2766 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 318450 | 210959 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4BG | NP234BG | np23 4bg | np234bg | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2701 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 318494 | 211012 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4BN | NP234BN | np23 4bn | np234bn | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2686 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 318479 | 211067 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4BP | NP234BP | np23 4bp | np234bp | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1400 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 319567 | 211757 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4BQ | NP234BQ | np23 4bq | np234bq | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2664 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 318531 | 211023 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4BR | NP234BR | np23 4br | np234br | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1804 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 319278 | 211450 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4BS | NP234BS | np23 4bs | np234bs | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1343 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 319693 | 211656 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4BT | NP234BT | np23 4bt | np234bt | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1478 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319408 | 211928 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4BU | NP234BU | np23 4bu | np234bu | Monmouthshire | Sir Fynwy | Brynmawr STW | 946 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 320473 | 211523 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP23 4BW | NP234BW | np23 4bw | np234bw | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2725 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 318427 | 211080 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4BX | NP234BX | np23 4bx | np234bx | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1626 | 1521 | Over1500 | 3.04 | 2.23 | 1.63 | 28.35 | 15.12 | 16.71 | 319536 | 211393 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DA | NP234DA | np23 4da | np234da | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1660 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319225 | 211900 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DB | NP234DB | np23 4db | np234db | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1769 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319109 | 211908 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DD | NP234DD | np23 4dd | np234dd | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1771 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319116 | 211877 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DE | NP234DE | np23 4de | np234de | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1545 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319323 | 211975 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DF | NP234DF | np23 4df | np234df | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1785 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319110 | 211850 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DG | NP234DG | np23 4dg | np234dg | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1420 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319427 | 212067 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DH | NP234DH | np23 4dh | np234dh | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1713 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319149 | 211971 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DJ | NP234DJ | np23 4dj | np234dj | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1459 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319398 | 212023 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DL | NP234DL | np23 4dl | np234dl | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1664 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319223 | 211896 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DN | NP234DN | np23 4dn | np234dn | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1695 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319189 | 211901 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DP | NP234DP | np23 4dp | np234dp | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1669 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319266 | 211764 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DQ | NP234DQ | np23 4dq | np234dq | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1572 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319276 | 212044 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DR | NP234DR | np23 4dr | np234dr | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1350 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 319518 | 212004 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DS | NP234DS | np23 4ds | np234ds | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1319 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 319573 | 211939 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DT | NP234DT | np23 4dt | np234dt | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1553 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319404 | 211741 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DU | NP234DU | np23 4du | np234du | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1497 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319423 | 211834 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DW | NP234DW | np23 4dw | np234dw | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1660 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319212 | 211945 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DX | NP234DX | np23 4dx | np234dx | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1514 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319450 | 211735 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DY | NP234DY | np23 4dy | np234dy | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1594 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319300 | 211884 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4DZ | NP234DZ | np23 4dz | np234dz | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1520 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319373 | 211902 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EA | NP234EA | np23 4ea | np234ea | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1543 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319430 | 211709 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EB | NP234EB | np23 4eb | np234eb | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1574 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319413 | 211676 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4ED | NP234ED | np23 4ed | np234ed | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1640 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319330 | 211694 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EE | NP234EE | np23 4ee | np234ee | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2452 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 318646 | 211249 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EF | NP234EF | np23 4ef | np234ef | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1743 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319262 | 211599 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EG | NP234EG | np23 4eg | np234eg | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2355 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 318685 | 211385 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EH | NP234EH | np23 4eh | np234eh | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1706 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319266 | 211674 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EJ | NP234EJ | np23 4ej | np234ej | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1743 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319233 | 211657 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EL | NP234EL | np23 4el | np234el | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1773 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319188 | 211684 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EN | NP234EN | np23 4en | np234en | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2429 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 318711 | 211179 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EP | NP234EP | np23 4ep | np234ep | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2048 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318888 | 211690 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EQ | NP234EQ | np23 4eq | np234eq | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2014 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318904 | 211745 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4ER | NP234ER | np23 4er | np234er | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2011 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318877 | 211840 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4ES | NP234ES | np23 4es | np234es | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1727 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319159 | 211888 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4ET | NP234ET | np23 4et | np234et | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1983 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318934 | 211755 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EU | NP234EU | np23 4eu | np234eu | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2047 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318874 | 211731 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EW | NP234EW | np23 4ew | np234ew | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2101 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318810 | 211753 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EX | NP234EX | np23 4ex | np234ex | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2098 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318809 | 211766 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EY | NP234EY | np23 4ey | np234ey | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1964 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318943 | 211786 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4EZ | NP234EZ | np23 4ez | np234ez | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2079 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318830 | 211761 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4FA | NP234FA | np23 4fa | np234fa | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1664 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319285 | 211733 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4FB | NP234FB | np23 4fb | np234fb | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1613 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319322 | 211777 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4FD | NP234FD | np23 4fd | np234fd | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1790 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319087 | 211907 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4FE | NP234FE | np23 4fe | np234fe | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1839 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319076 | 211784 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4GA | NP234GA | np23 4ga | np234ga | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 503 | 1488 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.73 | 14.79 | 16.35 | 320579 | 212858 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP23 4GB | NP234GB | np23 4gb | np234gb | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1225 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 319736 | 211811 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4GU | NP234GU | np23 4gu | np234gu | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 589 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 320217 | 212378 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP23 4HA | NP234HA | np23 4ha | np234ha | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2125 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318778 | 211772 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HB | NP234HB | np23 4hb | np234hb | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2173 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318753 | 211695 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HD | NP234HD | np23 4hd | np234hd | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2242 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318674 | 211715 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HE | NP234HE | np23 4he | np234he | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2410 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318498 | 211714 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HF | NP234HF | np23 4hf | np234hf | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2552 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318340 | 211753 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HG | NP234HG | np23 4hg | np234hg | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2485 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318443 | 211641 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HH | NP234HH | np23 4hh | np234hh | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2324 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318572 | 211768 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HJ | NP234HJ | np23 4hj | np234hj | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2671 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318210 | 211781 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HL | NP234HL | np23 4hl | np234hl | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2348 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318576 | 211673 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HN | NP234HN | np23 4hn | np234hn | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2706 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318248 | 211527 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HP | NP234HP | np23 4hp | np234hp | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2420 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318510 | 211645 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HQ | NP234HQ | np23 4hq | np234hq | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2444 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318525 | 211531 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HR | NP234HR | np23 4hr | np234hr | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2372 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318584 | 211577 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HS | NP234HS | np23 4hs | np234hs | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2765 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318125 | 211732 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HT | NP234HT | np23 4ht | np234ht | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2690 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318231 | 211632 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HU | NP234HU | np23 4hu | np234hu | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2709 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318192 | 211696 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HW | NP234HW | np23 4hw | np234hw | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2514 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 318464 | 211495 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HX | NP234HX | np23 4hx | np234hx | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2586 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318335 | 211645 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HY | NP234HY | np23 4hy | np234hy | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2587 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318350 | 211596 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4HZ | NP234HZ | np23 4hz | np234hz | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2746 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318185 | 211590 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4JA | NP234JA | np23 4ja | np234ja | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2554 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318357 | 211684 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4JB | NP234JB | np23 4jb | np234jb | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2746 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318128 | 211803 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4JD | NP234JD | np23 4jd | np234jd | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2903 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317939 | 211955 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4JP | NP234JP | np23 4jp | np234jp | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1903 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318995 | 211824 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4JY | NP234JY | np23 4jy | np234jy | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1951 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318993 | 211688 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4JZ | NP234JZ | np23 4jz | np234jz | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1953 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318967 | 211750 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4NA | NP234NA | np23 4na | np234na | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1897 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319097 | 211584 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4NH | NP234NH | np23 4nh | np234nh | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2166 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 319473 | 210702 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4NR | NP234NR | np23 4nr | np234nr | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2242 | 1521 | Over1500 | 3.04 | 2.23 | 1.63 | 28.35 | 15.12 | 16.71 | 319547 | 210554 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4NT | NP234NT | np23 4nt | np234nt | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1825 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 319489 | 211146 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4PS | NP234PS | np23 4ps | np234ps | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1934 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319050 | 211597 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4PW | NP234PW | np23 4pw | np234pw | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2045 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318948 | 211555 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4QA | NP234QA | np23 4qa | np234qa | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1739 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319093 | 212106 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4QN | NP234QN | np23 4qn | np234qn | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1590 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319220 | 212291 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RA | NP234RA | np23 4ra | np234ra | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1715 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319133 | 212029 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RB | NP234RB | np23 4rb | np234rb | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1781 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319071 | 212003 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RD | NP234RD | np23 4rd | np234rd | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1804 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319044 | 212019 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RE | NP234RE | np23 4re | np234re | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1289 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 319548 | 212127 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RF | NP234RF | np23 4rf | np234rf | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1710 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319146 | 211998 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RG | NP234RG | np23 4rg | np234rg | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1899 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318968 | 211930 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RH | NP234RH | np23 4rh | np234rh | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1639 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319207 | 212047 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RJ | NP234RJ | np23 4rj | np234rj | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2025 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318818 | 212020 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RL | NP234RL | np23 4rl | np234rl | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1942 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318915 | 211966 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RN | NP234RN | np23 4rn | np234rn | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1841 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318994 | 212081 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RP | NP234RP | np23 4rp | np234rp | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1816 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318994 | 212286 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RQ | NP234RQ | np23 4rq | np234rq | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1924 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318950 | 211900 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RR | NP234RR | np23 4rr | np234rr | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1630 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319177 | 212468 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RS | NP234RS | np23 4rs | np234rs | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1682 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319124 | 212392 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RT | NP234RT | np23 4rt | np234rt | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1664 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319142 | 212361 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RU | NP234RU | np23 4ru | np234ru | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1549 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319257 | 212362 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RW | NP234RW | np23 4rw | np234rw | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1783 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319029 | 212257 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RX | NP234RX | np23 4rx | np234rx | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2013 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318839 | 211979 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RY | NP234RY | np23 4ry | np234ry | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2011 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318812 | 212142 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4RZ | NP234RZ | np23 4rz | np234rz | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1880 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318948 | 212117 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SA | NP234SA | np23 4sa | np234sa | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1461 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319373 | 212123 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SB | NP234SB | np23 4sb | np234sb | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2005 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318827 | 212084 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SD | NP234SD | np23 4sd | np234sd | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1402 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319425 | 212167 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SE | NP234SE | np23 4se | np234se | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1407 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319400 | 212335 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SF | NP234SF | np23 4sf | np234sf | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1555 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319274 | 212142 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SG | NP234SG | np23 4sg | np234sg | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1956 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318880 | 212065 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SH | NP234SH | np23 4sh | np234sh | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1249 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 319601 | 212079 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SJ | NP234SJ | np23 4sj | np234sj | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1335 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319483 | 212228 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SL | NP234SL | np23 4sl | np234sl | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2227 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 318814 | 211412 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SN | NP234SN | np23 4sn | np234sn | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1757 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319061 | 212201 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SP | NP234SP | np23 4sp | np234sp | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1831 | 1582 | Over1500 | 3.17 | 2.32 | 1.7 | 29.49 | 15.73 | 17.38 | 319075 | 213007 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP23 4SR | NP234SR | np23 4sr | np234sr | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1365 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 319540 | 212922 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP23 4SS | NP234SS | np23 4ss | np234ss | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1961 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318928 | 211845 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4ST | NP234ST | np23 4st | np234st | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2328 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318541 | 211872 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SU | NP234SU | np23 4su | np234su | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2507 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318354 | 211884 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SX | NP234SX | np23 4sx | np234sx | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2120 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318742 | 211924 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SY | NP234SY | np23 4sy | np234sy | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2077 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318805 | 211853 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4SZ | NP234SZ | np23 4sz | np234sz | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2192 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318686 | 211851 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TA | NP234TA | np23 4ta | np234ta | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2070 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318785 | 211959 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TB | NP234TB | np23 4tb | np234tb | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2185 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318675 | 211925 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TD | NP234TD | np23 4td | np234td | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2129 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318713 | 212016 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TE | NP234TE | np23 4te | np234te | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2433 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318412 | 211973 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TF | NP234TF | np23 4tf | np234tf | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2423 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318405 | 212079 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TG | NP234TG | np23 4tg | np234tg | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2337 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318496 | 212052 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TH | NP234TH | np23 4th | np234th | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2269 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318585 | 211944 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TJ | NP234TJ | np23 4tj | np234tj | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2321 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318525 | 211976 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TL | NP234TL | np23 4tl | np234tl | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2356 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318497 | 211938 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TN | NP234TN | np23 4tn | np234tn | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2300 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318564 | 211894 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TP | NP234TP | np23 4tp | np234tp | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2165 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318731 | 211792 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TQ | NP234TQ | np23 4tq | np234tq | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2255 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318585 | 212016 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TR | NP234TR | np23 4tr | np234tr | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2379 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318504 | 211809 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TS | NP234TS | np23 4ts | np234ts | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2598 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318240 | 211999 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TT | NP234TT | np23 4tt | np234tt | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2593 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318236 | 212064 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TU | NP234TU | np23 4tu | np234tu | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2221 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318633 | 211950 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TW | NP234TW | np23 4tw | np234tw | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2246 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318648 | 211787 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TY | NP234TY | np23 4ty | np234ty | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2669 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318188 | 211888 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4TZ | NP234TZ | np23 4tz | np234tz | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2542 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 318312 | 211918 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4UT | NP234UT | np23 4ut | np234ut | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2708 | 1492 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.81 | 14.83 | 16.39 | 319959 | 209837 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4WH | NP234WH | np23 4wh | np234wh | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2778 | 1492 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.81 | 14.83 | 16.39 | 319970 | 209760 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4XR | NP234XR | np23 4xr | np234xr | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1883 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 318983 | 211936 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 4XT | NP234XT | np23 4xt | np234xt | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1166 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 319647 | 212541 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP23 4YG | NP234YG | np23 4yg | np234yg | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 1744 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 319134 | 211913 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5JZ | NP235JZ | np23 5jz | np235jz | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3411 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 317554 | 211380 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5QR | NP235QR | np23 5qr | np235qr | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3188 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317672 | 211826 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5QS | NP235QS | np23 5qs | np235qs | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3053 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317800 | 211875 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5QT | NP235QT | np23 5qt | np235qt | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3033 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317806 | 211964 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5QU | NP235QU | np23 5qu | np235qu | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3034 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317846 | 211741 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5QW | NP235QW | np23 5qw | np235qw | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3327 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317546 | 211744 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5QX | NP235QX | np23 5qx | np235qx | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3053 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317809 | 211828 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5QY | NP235QY | np23 5qy | np235qy | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3121 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317756 | 211745 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5QZ | NP235QZ | np23 5qz | np235qz | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2972 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317900 | 211785 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5RA | NP235RA | np23 5ra | np235ra | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3169 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317672 | 211939 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5RB | NP235RB | np23 5rb | np235rb | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3241 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317629 | 211770 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5RD | NP235RD | np23 5rd | np235rd | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3275 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317587 | 211807 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5RE | NP235RE | np23 5re | np235re | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3424 | 1536 | Over1500 | 3.07 | 2.25 | 1.65 | 28.63 | 15.27 | 16.88 | 317450 | 211729 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5RG | NP235RG | np23 5rg | np235rg | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3558 | 1536 | Over1500 | 3.07 | 2.25 | 1.65 | 28.63 | 15.27 | 16.88 | 317305 | 211774 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5RT | NP235RT | np23 5rt | np235rt | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2941 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317913 | 211878 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5RX | NP235RX | np23 5rx | np235rx | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 2978 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317866 | 211935 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5RY | NP235RY | np23 5ry | np235ry | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3366 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 317589 | 211419 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP23 5TB | NP235TB | np23 5tb | np235tb | Blaenau Gwent | Blaenau Gwent | Brynmawr STW | 3119 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 317715 | 211991 | Blaenau Gwent LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council
NP25 4AX | NP254AX | np25 4ax | np254ax | Monmouthshire | Sir Fynwy | Trellech STW | 312 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 350098 | 205741 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AY | NP254AY | np25 4ay | np254ay | Monmouthshire | Sir Fynwy | Trellech STW | 363 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 350213 | 205684 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BN | NP254BN | np25 4bn | np254bn | Monmouthshire | Sir Fynwy | Dingestow STW | 2369 | 914 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.04 | 9.09 | 10.04 | 344860 | 207918 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BT | NP254BT | np25 4bt | np254bt | Monmouthshire | Sir Fynwy | Raglan STW | 3293 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 344478 | 205481 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BU | NP254BU | np25 4bu | np254bu | Monmouthshire | Sir Fynwy | Llanishen STW | 3002 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 345400 | 205076 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DA | NP254DA | np25 4da | np254da | Monmouthshire | Sir Fynwy | Dingestow STW | 3290 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 346007 | 206763 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4NY | NP254NY | np25 4ny | np254ny | Monmouthshire | Sir Fynwy | Trellech STW | 248 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 350138 | 205431 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4NZ | NP254NZ | np25 4nz | np254nz | Monmouthshire | Sir Fynwy | Trellech STW | 277 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 349936 | 205775 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PA | NP254PA | np25 4pa | np254pa | Monmouthshire | Sir Fynwy | Trellech STW | 195 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 350095 | 205492 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PB | NP254PB | np25 4pb | np254pb | Monmouthshire | Sir Fynwy | Trellech STW | 229 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 349965 | 205719 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PD | NP254PD | np25 4pd | np254pd | Monmouthshire | Sir Fynwy | Trellech STW | 322 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 350051 | 205784 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PE | NP254PE | np25 4pe | np254pe | Monmouthshire | Sir Fynwy | Trellech STW | 326 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 350069 | 205221 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PF | NP254PF | np25 4pf | np254pf | Monmouthshire | Sir Fynwy | Trellech STW | 481 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 349752 | 205043 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PG | NP254PG | np25 4pg | np254pg | Monmouthshire | Sir Fynwy | Trellech STW | 580 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 349609 | 206002 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PH | NP254PH | np25 4ph | np254ph | Monmouthshire | Sir Fynwy | Trellech STW | 1048 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 350248 | 206488 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PP | NP254PP | np25 4pp | np254pp | Monmouthshire | Sir Fynwy | Trellech STW | 2850 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 347090 | 205970 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PQ | NP254PQ | np25 4pq | np254pq | Monmouthshire | Sir Fynwy | Trellech STW | 739 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 350416 | 206029 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PR | NP254PR | np25 4pr | np254pr | Monmouthshire | Sir Fynwy | Trellech STW | 1221 | 1126 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.99 | 11.19 | 12.37 | 350948 | 204875 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PS | NP254PS | np25 4ps | np254ps | Monmouthshire | Sir Fynwy | Trellech STW | 1251 | 1126 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.99 | 11.19 | 12.37 | 350824 | 204658 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PX | NP254PX | np25 4px | np254px | Monmouthshire | Sir Fynwy | Trellech STW | 1288 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 350108 | 204229 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PY | NP254PY | np25 4py | np254py | Monmouthshire | Sir Fynwy | Trellech STW | 1412 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 348518 | 205213 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PZ | NP254PZ | np25 4pz | np254pz | Monmouthshire | Sir Fynwy | Trellech STW | 557 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 350251 | 205068 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QB | NP254QB | np25 4qb | np254qb | Monmouthshire | Sir Fynwy | Trellech STW | 1258 | 1126 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.99 | 11.19 | 12.37 | 350888 | 204722 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4RB | NP254RB | np25 4rb | np254rb | Monmouthshire | Sir Fynwy | Trellech STW | 307 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 350019 | 205783 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4SD | NP254SD | np25 4sd | np254sd | Monmouthshire | Sir Fynwy | Trellech STW | 292 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 350191 | 205516 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AA | NP40AA | np4 0aa | np40aa | Monmouthshire | Sir Fynwy | Goytre STW | 1461 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 333017 | 205147 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AB | NP40AB | np4 0ab | np40ab | Monmouthshire | Sir Fynwy | Goytre STW | 1603 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 332854 | 205333 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AD | NP40AD | np4 0ad | np40ad | Monmouthshire | Sir Fynwy | Goytre STW | 2551 | 1245 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.2 | 12.38 | 13.68 | 331922 | 205702 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AE | NP40AE | np4 0ae | np40ae | Monmouthshire | Sir Fynwy | Goytre STW | 3025 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 331483 | 205965 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AF | NP40AF | np4 0af | np40af | Monmouthshire | Sir Fynwy | Little Mill STW | 2324 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 331998 | 203926 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AG | NP40AG | np4 0ag | np40ag | Monmouthshire | Sir Fynwy | Goytre STW | 2569 | 1245 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.2 | 12.38 | 13.68 | 331890 | 205529 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AH | NP40AH | np4 0ah | np40ah | Monmouthshire | Sir Fynwy | Goytre STW | 2387 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332223 | 204561 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AJ | NP40AJ | np4 0aj | np40aj | Monmouthshire | Sir Fynwy | Goytre STW | 2191 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332442 | 204543 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AL | NP40AL | np4 0al | np40al | Monmouthshire | Sir Fynwy | Goytre STW | 2120 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 332659 | 204280 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AN | NP40AN | np4 0an | np40an | Monmouthshire | Sir Fynwy | Goytre STW | 2267 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 332441 | 204367 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AP | NP40AP | np4 0ap | np40ap | Monmouthshire | Sir Fynwy | Goytre STW | 2174 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332382 | 204752 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AQ | NP40AQ | np4 0aq | np40aq | Monmouthshire | Sir Fynwy | Goytre STW | 2260 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332282 | 204786 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AR | NP40AR | np4 0ar | np40ar | Monmouthshire | Sir Fynwy | Goytre STW | 2200 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332365 | 204719 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AS | NP40AS | np4 0as | np40as | Monmouthshire | Sir Fynwy | Goytre STW | 2162 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332365 | 204854 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AT | NP40AT | np4 0at | np40at | Monmouthshire | Sir Fynwy | Goytre STW | 2090 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332424 | 204915 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AU | NP40AU | np4 0au | np40au | Monmouthshire | Sir Fynwy | Goytre STW | 2048 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332495 | 204812 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AW | NP40AW | np4 0aw | np40aw | Monmouthshire | Sir Fynwy | Goytre STW | 1971 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 332536 | 204958 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AX | NP40AX | np4 0ax | np40ax | Monmouthshire | Sir Fynwy | Goytre STW | 2044 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332449 | 205015 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AY | NP40AY | np4 0ay | np40ay | Monmouthshire | Sir Fynwy | Goytre STW | 2125 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332382 | 204942 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0AZ | NP40AZ | np4 0az | np40az | Monmouthshire | Sir Fynwy | Goytre STW | 1776 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 332690 | 205214 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BA | NP40BA | np4 0ba | np40ba | Monmouthshire | Sir Fynwy | Goytre STW | 2290 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332259 | 204757 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BB | NP40BB | np4 0bb | np40bb | Monmouthshire | Sir Fynwy | Goytre STW | 1856 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 332609 | 205220 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BD | NP40BD | np4 0bd | np40bd | Monmouthshire | Sir Fynwy | Goytre STW | 1985 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 332504 | 205041 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BE | NP40BE | np4 0be | np40be | Monmouthshire | Sir Fynwy | Goytre STW | 1841 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 332618 | 205298 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BG | NP40BG | np4 0bg | np40bg | Monmouthshire | Sir Fynwy | Goytre STW | 2190 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332311 | 204962 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BH | NP40BH | np4 0bh | np40bh | Monmouthshire | Sir Fynwy | Goytre STW | 2180 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332333 | 204909 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BJ | NP40BJ | np4 0bj | np40bj | Monmouthshire | Sir Fynwy | Goytre STW | 2746 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 331740 | 204998 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BL | NP40BL | np4 0bl | np40bl | Monmouthshire | Sir Fynwy | Goytre STW | 2359 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332219 | 204656 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BN | NP40BN | np4 0bn | np40bn | Monmouthshire | Sir Fynwy | Goytre STW | 3019 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 331479 | 205908 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BP | NP40BP | np4 0bp | np40bp | Monmouthshire | Sir Fynwy | Goytre STW | 2231 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332258 | 205022 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BQ | NP40BQ | np4 0bq | np40bq | Monmouthshire | Sir Fynwy | Goytre STW | 2182 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332306 | 205032 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BR | NP40BR | np4 0br | np40br | Monmouthshire | Sir Fynwy | Goytre STW | 1988 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332480 | 205186 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BS | NP40BS | np4 0bs | np40bs | Monmouthshire | Sir Fynwy | Goytre STW | 2002 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 332463 | 205216 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BW | NP40BW | np4 0bw | np40bw | Monmouthshire | Sir Fynwy | Goytre STW | 2462 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 332193 | 204435 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0BX | NP40BX | np4 0bx | np40bx | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4983 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330349 | 198739 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0BY | NP40BY | np4 0by | np40by | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4889 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330462 | 198722 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0BZ | NP40BZ | np4 0bz | np40bz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4869 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330444 | 198673 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0DA | NP40DA | np4 0da | np40da | Torfaen | Tor-Faen | Little Mill STW | 4534 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330572 | 199169 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0DB | NP40DB | np4 0db | np40db | Monmouthshire | Sir Fynwy | Goytre STW | 2441 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 332235 | 204391 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0DD | NP40DD | np4 0dd | np40dd | Monmouthshire | Sir Fynwy | Little Mill STW | 2507 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 332167 | 204343 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0DE | NP40DE | np4 0de | np40de | Torfaen | Tor-Faen | Little Mill STW | 3828 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330648 | 200159 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0DF | NP40DF | np4 0df | np40df | Torfaen | Tor-Faen | Little Mill STW | 3959 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330570 | 200044 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0DG | NP40DG | np4 0dg | np40dg | Torfaen | Tor-Faen | Little Mill STW | 4054 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330440 | 200061 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0DL | NP40DL | np4 0dl | np40dl | Monmouthshire | Sir Fynwy | Goytre STW | 2531 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 332099 | 204483 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0DQ | NP40DQ | np4 0dq | np40dq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4854 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329854 | 198891 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0EX | NP40EX | np4 0ex | np40ex | Torfaen | Tor-Faen | Little Mill STW | 3905 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330544 | 200172 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0EY | NP40EY | np4 0ey | np40ey | Torfaen | Tor-Faen | Little Mill STW | 3790 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330746 | 200091 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0EZ | NP40EZ | np4 0ez | np40ez | Torfaen | Tor-Faen | Little Mill STW | 3791 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330704 | 200146 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0HA | NP40HA | np4 0ha | np40ha | Monmouthshire | Sir Fynwy | Little Mill STW | 1671 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332247 | 203128 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HB | NP40HB | np4 0hb | np40hb | Monmouthshire | Sir Fynwy | Little Mill STW | 1619 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332261 | 203034 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HD | NP40HD | np4 0hd | np40hd | Torfaen | Tor-Faen | Little Mill STW | 2256 | 1252 | 1200to1500 | 2.51 | 1.83 | 1.34 | 23.34 | 12.45 | 13.76 | 331500 | 202243 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0HE | NP40HE | np4 0he | np40he | Monmouthshire | Sir Fynwy | Little Mill STW | 1833 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 331983 | 202885 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HF | NP40HF | np4 0hf | np40hf | Monmouthshire | Sir Fynwy | Little Mill STW | 1838 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 331988 | 202920 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HG | NP40HG | np4 0hg | np40hg | Monmouthshire | Sir Fynwy | Little Mill STW | 1821 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 331998 | 202893 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HH | NP40HH | np4 0hh | np40hh | Monmouthshire | Sir Fynwy | Little Mill STW | 1777 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332057 | 202939 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HJ | NP40HJ | np4 0hj | np40hj | Monmouthshire | Sir Fynwy | Little Mill STW | 1759 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332083 | 202958 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HL | NP40HL | np4 0hl | np40hl | Monmouthshire | Sir Fynwy | Little Mill STW | 1525 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332352 | 203008 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HN | NP40HN | np4 0hn | np40hn | Monmouthshire | Sir Fynwy | Little Mill STW | 1592 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332253 | 202940 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HP | NP40HP | np4 0hp | np40hp | Monmouthshire | Sir Fynwy | Little Mill STW | 1614 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332286 | 203078 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HQ | NP40HQ | np4 0hq | np40hq | Monmouthshire | Sir Fynwy | Little Mill STW | 1697 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332458 | 203500 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HR | NP40HR | np4 0hr | np40hr | Monmouthshire | Sir Fynwy | Little Mill STW | 1884 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332107 | 203320 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HS | NP40HS | np4 0hs | np40hs | Monmouthshire | Sir Fynwy | Little Mill STW | 1843 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 331995 | 202960 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HT | NP40HT | np4 0ht | np40ht | Monmouthshire | Sir Fynwy | Little Mill STW | 1703 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332182 | 203064 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HU | NP40HU | np4 0hu | np40hu | Monmouthshire | Sir Fynwy | Little Mill STW | 1802 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332073 | 203059 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HW | NP40HW | np4 0hw | np40hw | Monmouthshire | Sir Fynwy | Little Mill STW | 1745 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332114 | 203004 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HX | NP40HX | np4 0hx | np40hx | Monmouthshire | Sir Fynwy | Little Mill STW | 1500 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 332413 | 203078 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HY | NP40HY | np4 0hy | np40hy | Monmouthshire | Sir Fynwy | Little Mill STW | 1406 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 332502 | 203047 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0HZ | NP40HZ | np4 0hz | np40hz | Torfaen | Tor-Faen | Little Mill STW | 2913 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 330846 | 202609 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0JA | NP40JA | np4 0ja | np40ja | Torfaen | Tor-Faen | Little Mill STW | 2961 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 330846 | 201829 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0JB | NP40JB | np4 0jb | np40jb | Torfaen | Tor-Faen | Little Mill STW | 3547 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 330400 | 201239 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0JD | NP40JD | np4 0jd | np40jd | Monmouthshire | Sir Fynwy | Little Mill STW | 2733 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 331471 | 203906 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0JE | NP40JE | np4 0je | np40je | Monmouthshire | Sir Fynwy | Little Mill STW | 2107 | 1241 | 1200to1500 | 2.48 | 1.82 | 1.33 | 23.13 | 12.34 | 13.63 | 331794 | 203182 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0JF | NP40JF | np4 0jf | np40jf | Monmouthshire | Sir Fynwy | Little Mill STW | 3192 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 330663 | 203207 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0JG | NP40JG | np4 0jg | np40jg | Monmouthshire | Sir Fynwy | Little Mill STW | 3608 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 330590 | 204139 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0JH | NP40JH | np4 0jh | np40jh | Monmouthshire | Sir Fynwy | Little Mill STW | 3009 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 331033 | 203690 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0JJ | NP40JJ | np4 0jj | np40jj | Monmouthshire | Sir Fynwy | Little Mill STW | 2572 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 331191 | 202651 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0JL | NP40JL | np4 0jl | np40jl | Torfaen | Tor-Faen | Little Mill STW | 2573 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 331191 | 202137 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0JN | NP40JN | np4 0jn | np40jn | Torfaen | Tor-Faen | Little Mill STW | 2563 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 331215 | 202029 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0JR | NP40JR | np4 0jr | np40jr | Torfaen | Tor-Faen | Little Mill STW | 4095 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330561 | 199833 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0LS | NP40LS | np4 0ls | np40ls | Torfaen | Tor-Faen | Pantygasseg WwTW | 4570 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329665 | 199571 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0LT | NP40LT | np4 0lt | np40lt | Torfaen | Tor-Faen | Little Mill STW | 3641 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330866 | 200179 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0LU | NP40LU | np4 0lu | np40lu | Torfaen | Tor-Faen | Little Mill STW | 3551 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330887 | 200301 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0LW | NP40LW | np4 0lw | np40lw | Torfaen | Tor-Faen | Little Mill STW | 3509 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330963 | 200270 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0LX | NP40LX | np4 0lx | np40lx | Torfaen | Tor-Faen | Little Mill STW | 3708 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330909 | 200019 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0LY | NP40LY | np4 0ly | np40ly | Torfaen | Tor-Faen | Little Mill STW | 3740 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330857 | 200031 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0LZ | NP40LZ | np4 0lz | np40lz | Torfaen | Tor-Faen | Little Mill STW | 3843 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330802 | 199937 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NA | NP40NA | np4 0na | np40na | Torfaen | Tor-Faen | Little Mill STW | 4361 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330626 | 199360 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NB | NP40NB | np4 0nb | np40nb | Torfaen | Tor-Faen | Little Mill STW | 4277 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330618 | 199490 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0ND | NP40ND | np4 0nd | np40nd | Torfaen | Tor-Faen | Little Mill STW | 4171 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330618 | 199648 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NE | NP40NE | np4 0ne | np40ne | Torfaen | Tor-Faen | Little Mill STW | 4182 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330691 | 199550 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NF | NP40NF | np4 0nf | np40nf | Torfaen | Tor-Faen | Little Mill STW | 4273 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330679 | 199431 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NG | NP40NG | np4 0ng | np40ng | Torfaen | Tor-Faen | Little Mill STW | 3931 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330809 | 199793 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NH | NP40NH | np4 0nh | np40nh | Torfaen | Tor-Faen | Little Mill STW | 4079 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330752 | 199636 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NJ | NP40NJ | np4 0nj | np40nj | Torfaen | Tor-Faen | Little Mill STW | 3813 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330852 | 199924 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NL | NP40NL | np4 0nl | np40nl | Torfaen | Tor-Faen | Little Mill STW | 3911 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330807 | 199827 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NN | NP40NN | np4 0nn | np40nn | Torfaen | Tor-Faen | Little Mill STW | 3801 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330904 | 199882 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NP | NP40NP | np4 0np | np40np | Torfaen | Tor-Faen | Little Mill STW | 3756 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330939 | 199911 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NQ | NP40NQ | np4 0nq | np40nq | Torfaen | Tor-Faen | Little Mill STW | 3982 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330751 | 199783 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NR | NP40NR | np4 0nr | np40nr | Torfaen | Tor-Faen | Little Mill STW | 4093 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330798 | 199567 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NS | NP40NS | np4 0ns | np40ns | Torfaen | Tor-Faen | Little Mill STW | 4345 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330710 | 199297 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NT | NP40NT | np4 0nt | np40nt | Torfaen | Tor-Faen | Little Mill STW | 4695 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330547 | 198969 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NU | NP40NU | np4 0nu | np40nu | Torfaen | Tor-Faen | Little Mill STW | 4823 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330548 | 198796 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NW | NP40NW | np4 0nw | np40nw | Torfaen | Tor-Faen | Little Mill STW | 3879 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330871 | 199803 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NX | NP40NX | np4 0nx | np40nx | Torfaen | Tor-Faen | Little Mill STW | 4737 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330486 | 198969 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NY | NP40NY | np4 0ny | np40ny | Torfaen | Tor-Faen | Little Mill STW | 4980 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330316 | 198795 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0NZ | NP40NZ | np4 0nz | np40nz | Torfaen | Tor-Faen | Little Mill STW | 4922 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330376 | 198819 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PA | NP40PA | np4 0pa | np40pa | Torfaen | Tor-Faen | Little Mill STW | 4729 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330447 | 199018 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PB | NP40PB | np4 0pb | np40pb | Torfaen | Tor-Faen | Little Mill STW | 4815 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330370 | 198973 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PE | NP40PE | np4 0pe | np40pe | Torfaen | Tor-Faen | Little Mill STW | 4874 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330453 | 198813 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PF | NP40PF | np4 0pf | np40pf | Torfaen | Tor-Faen | Little Mill STW | 3989 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330671 | 199866 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PG | NP40PG | np4 0pg | np40pg | Torfaen | Tor-Faen | Little Mill STW | 4460 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329945 | 200076 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PH | NP40PH | np4 0ph | np40ph | Torfaen | Tor-Faen | Little Mill STW | 4472 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330243 | 199627 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PJ | NP40PJ | np4 0pj | np40pj | Torfaen | Tor-Faen | Little Mill STW | 4527 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330294 | 199478 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PL | NP40PL | np4 0pl | np40pl | Torfaen | Tor-Faen | Little Mill STW | 4521 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330395 | 199372 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PN | NP40PN | np4 0pn | np40pn | Torfaen | Tor-Faen | Little Mill STW | 4548 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330379 | 199349 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PP | NP40PP | np4 0pp | np40pp | Torfaen | Tor-Faen | Little Mill STW | 4377 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330244 | 199783 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PQ | NP40PQ | np4 0pq | np40pq | Torfaen | Tor-Faen | Little Mill STW | 4436 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330118 | 199856 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PR | NP40PR | np4 0pr | np40pr | Torfaen | Tor-Faen | Little Mill STW | 4201 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330426 | 199834 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PS | NP40PS | np4 0ps | np40ps | Torfaen | Tor-Faen | Little Mill STW | 4272 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330372 | 199788 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PT | NP40PT | np4 0pt | np40pt | Torfaen | Tor-Faen | Little Mill STW | 4385 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330374 | 199604 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PU | NP40PU | np4 0pu | np40pu | Torfaen | Tor-Faen | Little Mill STW | 4323 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330458 | 199600 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PW | NP40PW | np4 0pw | np40pw | Torfaen | Tor-Faen | Little Mill STW | 4607 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330508 | 199129 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PX | NP40PX | np4 0px | np40px | Torfaen | Tor-Faen | Little Mill STW | 4472 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330362 | 199483 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PY | NP40PY | np4 0py | np40py | Torfaen | Tor-Faen | Little Mill STW | 4430 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330396 | 199508 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0PZ | NP40PZ | np4 0pz | np40pz | Torfaen | Tor-Faen | Little Mill STW | 4609 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330174 | 199495 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QA | NP40QA | np4 0qa | np40qa | Torfaen | Tor-Faen | Little Mill STW | 4612 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330352 | 199284 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QB | NP40QB | np4 0qb | np40qb | Torfaen | Tor-Faen | Little Mill STW | 4639 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330253 | 199355 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QD | NP40QD | np4 0qd | np40qd | Torfaen | Tor-Faen | Little Mill STW | 4218 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330152 | 200202 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QE | NP40QE | np4 0qe | np40qe | Torfaen | Tor-Faen | Little Mill STW | 4682 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330331 | 199204 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QF | NP40QF | np4 0qf | np40qf | Torfaen | Tor-Faen | Little Mill STW | 4727 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330259 | 199216 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QG | NP40QG | np4 0qg | np40qg | Torfaen | Tor-Faen | Little Mill STW | 4278 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330208 | 200003 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QH | NP40QH | np4 0qh | np40qh | Torfaen | Tor-Faen | Little Mill STW | 4464 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329890 | 200160 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QJ | NP40QJ | np4 0qj | np40qj | Torfaen | Tor-Faen | Little Mill STW | 4412 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330001 | 200077 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QL | NP40QL | np4 0ql | np40ql | Torfaen | Tor-Faen | Little Mill STW | 4398 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330116 | 199925 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QN | NP40QN | np4 0qn | np40qn | Torfaen | Tor-Faen | Little Mill STW | 4299 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330283 | 199861 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QP | NP40QP | np4 0qp | np40qp | Torfaen | Tor-Faen | Little Mill STW | 4277 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330248 | 199947 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QQ | NP40QQ | np4 0qq | np40qq | Torfaen | Tor-Faen | Little Mill STW | 4114 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330327 | 200121 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QR | NP40QR | np4 0qr | np40qr | Torfaen | Tor-Faen | Little Mill STW | 4169 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330367 | 199966 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QS | NP40QS | np4 0qs | np40qs | Torfaen | Tor-Faen | Little Mill STW | 4233 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330180 | 200128 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QT | NP40QT | np4 0qt | np40qt | Torfaen | Tor-Faen | Little Mill STW | 4349 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330197 | 199894 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QU | NP40QU | np4 0qu | np40qu | Torfaen | Tor-Faen | Little Mill STW | 4322 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330054 | 200163 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QW | NP40QW | np4 0qw | np40qw | Torfaen | Tor-Faen | Little Mill STW | 3990 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330629 | 199917 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QX | NP40QX | np4 0qx | np40qx | Torfaen | Tor-Faen | Little Mill STW | 3755 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 330496 | 200529 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QY | NP40QY | np4 0qy | np40qy | Torfaen | Tor-Faen | Pantygasseg WwTW | 4591 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329686 | 200249 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0QZ | NP40QZ | np4 0qz | np40qz | Torfaen | Tor-Faen | Little Mill STW | 4345 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330533 | 199482 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RA | NP40RA | np4 0ra | np40ra | Torfaen | Tor-Faen | Little Mill STW | 4392 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329873 | 200339 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RB | NP40RB | np4 0rb | np40rb | Torfaen | Tor-Faen | Little Mill STW | 4555 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329718 | 200284 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RD | NP40RD | np4 0rd | np40rd | Torfaen | Tor-Faen | Little Mill STW | 4459 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329783 | 200367 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RE | NP40RE | np4 0re | np40re | Torfaen | Tor-Faen | Little Mill STW | 4239 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330087 | 200269 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RF | NP40RF | np4 0rf | np40rf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4088 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329185 | 200201 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RG | NP40RG | np4 0rg | np40rg | Torfaen | Tor-Faen | Little Mill STW | 4474 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330547 | 199278 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RH | NP40RH | np4 0rh | np40rh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4253 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329358 | 200055 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RJ | NP40RJ | np4 0rj | np40rj | Torfaen | Tor-Faen | Little Mill STW | 4221 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330484 | 199729 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RN | NP40RN | np4 0rn | np40rn | Torfaen | Tor-Faen | Little Mill STW | 4359 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330180 | 199902 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RP | NP40RP | np4 0rp | np40rp | Torfaen | Tor-Faen | Little Mill STW | 4138 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330338 | 200061 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RR | NP40RR | np4 0rr | np40rr | Torfaen | Tor-Faen | Little Mill STW | 3947 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 330598 | 200027 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RS | NP40RS | np4 0rs | np40rs | Torfaen | Tor-Faen | Little Mill STW | 4071 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330491 | 199962 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RT | NP40RT | np4 0rt | np40rt | Torfaen | Tor-Faen | Little Mill STW | 4107 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330447 | 199961 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0RW | NP40RW | np4 0rw | np40rw | Torfaen | Tor-Faen | Little Mill STW | 4175 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330340 | 199994 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0SS | NP40SS | np4 0ss | np40ss | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 3127 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 333302 | 198397 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0ST | NP40ST | np4 0st | np40st | Torfaen | Tor-Faen | Little Mill STW | 4584 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329780 | 200111 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0SU | NP40SU | np4 0su | np40su | Torfaen | Tor-Faen | Little Mill STW | 4576 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329848 | 200013 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0SW | NP40SW | np4 0sw | np40sw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4731 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329831 | 199636 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0SX | NP40SX | np4 0sx | np40sx | Torfaen | Tor-Faen | Little Mill STW | 4020 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 331091 | 199387 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0SY | NP40SY | np4 0sy | np40sy | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 3042 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 333253 | 198298 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0SZ | NP40SZ | np4 0sz | np40sz | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 3187 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 333562 | 198506 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0TA | NP40TA | np4 0ta | np40ta | Torfaen | Tor-Faen | Little Mill STW | 3971 | 1266 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.6 | 12.58 | 13.91 | 331886 | 198895 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0TB | NP40TB | np4 0tb | np40tb | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 2943 | 1206 | 1200to1500 | 2.41 | 1.77 | 1.3 | 22.48 | 11.99 | 13.25 | 334893 | 198153 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0TE | NP40TE | np4 0te | np40te | Monmouthshire | Sir Fynwy | Little Mill STW | 1737 | 1195 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.27 | 11.88 | 13.13 | 334031 | 200686 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0TF | NP40TF | np4 0tf | np40tf | Monmouthshire | Sir Fynwy | Little Mill STW | 1093 | 1195 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.27 | 11.88 | 13.13 | 333608 | 201317 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0TG | NP40TG | np4 0tg | np40tg | Monmouthshire | Sir Fynwy | Little Mill STW | 1461 | 1243 | 1200to1500 | 2.49 | 1.82 | 1.33 | 23.17 | 12.36 | 13.66 | 333342 | 200998 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0TH | NP40TH | np4 0th | np40th | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 3367 | 1238 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.07 | 12.31 | 13.6 | 333481 | 198676 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0TJ | NP40TJ | np4 0tj | np40tj | Monmouthshire | Sir Fynwy | Little Mill STW | 3681 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 331144 | 199802 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0TL | NP40TL | np4 0tl | np40tl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4600 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329684 | 199439 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0TN | NP40TN | np4 0tn | np40tn | Torfaen | Tor-Faen | Little Mill STW | 4956 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 330163 | 198982 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0TP | NP40TP | np4 0tp | np40tp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4638 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 330396 | 198266 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0TQ | NP40TQ | np4 0tq | np40tq | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 3165 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 334070 | 198513 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0TS | NP40TS | np4 0ts | np40ts | Torfaen | Tor-Faen | Little Mill STW | 4536 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330774 | 198979 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0TT | NP40TT | np4 0tt | np40tt | Torfaen | Tor-Faen | Little Mill STW | 4520 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330630 | 199131 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0TU | NP40TU | np4 0tu | np40tu | Torfaen | Tor-Faen | Little Mill STW | 4407 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330692 | 199229 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0TW | NP40TW | np4 0tw | np40tw | Torfaen | Tor-Faen | Little Mill STW | 4679 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329938 | 199690 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0TX | NP40TX | np4 0tx | np40tx | Monmouthshire | Sir Fynwy | Little Mill STW | 2341 | 1288 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.01 | 12.8 | 14.15 | 332088 | 200753 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0TY | NP40TY | np4 0ty | np40ty | Monmouthshire | Sir Fynwy | Little Mill STW | 1461 | 1243 | 1200to1500 | 2.49 | 1.82 | 1.33 | 23.17 | 12.36 | 13.66 | 332774 | 201313 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0TZ | NP40TZ | np4 0tz | np40tz | Monmouthshire | Sir Fynwy | Little Mill STW | 867 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 333202 | 201729 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0UA | NP40UA | np4 0ua | np40ua | Monmouthshire | Sir Fynwy | Little Mill STW | 743 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 333296 | 201812 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0UB | NP40UB | np4 0ub | np40ub | Monmouthshire | Sir Fynwy | Little Mill STW | 618 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 333562 | 201812 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0UD | NP40UD | np4 0ud | np40ud | Monmouthshire | Sir Fynwy | Little Mill STW | 967 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 332988 | 202994 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0UE | NP40UE | np4 0ue | np40ue | Torfaen | Tor-Faen | Little Mill STW | 4378 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 330750 | 199214 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0XB | NP40XB | np4 0xb | np40xb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4401 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329508 | 199832 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0XG | NP40XG | np4 0xg | np40xg | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0XJ | NP40XJ | np4 0xj | np40xj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4385 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329490 | 200055 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0XS | NP40XS | np4 0xs | np40xs | Torfaen | Tor-Faen | Little Mill STW | 3013 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 330762 | 202779 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0XX | NP40XX | np4 0xx | np40xx | Torfaen | Tor-Faen | Little Mill STW | 2922 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 330847 | 202725 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0XZ | NP40XZ | np4 0xz | np40xz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4176 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329282 | 199779 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0YE | NP40YE | np4 0ye | np40ye | Monmouthshire | Sir Fynwy | Little Mill STW | 1682 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 332992 | 203901 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP4 0YJ | NP40YJ | np4 0yj | np40yj | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0YN | NP40YN | np4 0yn | np40yn | Torfaen | Tor-Faen | Little Mill STW | 4547 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 330001 | 199829 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0YP | NP40YP | np4 0yp | np40yp | Torfaen | Tor-Faen | Little Mill STW | 2880 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 330880 | 202624 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0YT | NP40YT | np4 0yt | np40yt | Torfaen | Tor-Faen | Little Mill STW | 2880 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 330880 | 202624 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 0YW | NP40YW | np4 0yw | np40yw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4650 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329734 | 199442 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4BG | NP44BG | np4 4bg | np44bg | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4BX | NP44BX | np4 4bx | np44bx | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4BY | NP44BY | np4 4by | np44by | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DE | NP44DE | np4 4de | np44de | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DF | NP44DF | np4 4df | np44df | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DG | NP44DG | np4 4dg | np44dg | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DH | NP44DH | np4 4dh | np44dh | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DJ | NP44DJ | np4 4dj | np44dj | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DL | NP44DL | np4 4dl | np44dl | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DN | NP44DN | np4 4dn | np44dn | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DP | NP44DP | np4 4dp | np44dp | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DR | NP44DR | np4 4dr | np44dr | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DS | NP44DS | np4 4ds | np44ds | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DW | NP44DW | np4 4dw | np44dw | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DY | NP44DY | np4 4dy | np44dy | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4DZ | NP44DZ | np4 4dz | np44dz | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4EJ | NP44EJ | np4 4ej | np44ej | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4SA | NP44SA | np4 4sa | np44sa | Torfaen | Tor-Faen | Pantygasseg WwTW | 3228 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328215 | 200779 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 4ZZ | NP44ZZ | np4 4zz | np44zz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3228 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328215 | 200779 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AA | NP45AA | np4 5aa | np45aa | Torfaen | Tor-Faen | Pantygasseg WwTW | 4276 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329085 | 198335 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AB | NP45AB | np4 5ab | np45ab | Torfaen | Tor-Faen | Pantygasseg WwTW | 4263 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329098 | 198406 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AD | NP45AD | np4 5ad | np45ad | Torfaen | Tor-Faen | Pantygasseg WwTW | 4146 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328957 | 198366 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AE | NP45AE | np4 5ae | np45ae | Torfaen | Tor-Faen | Pantygasseg WwTW | 4206 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328963 | 198224 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AF | NP45AF | np4 5af | np45af | Torfaen | Tor-Faen | Pantygasseg WwTW | 4159 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329035 | 198537 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AG | NP45AG | np4 5ag | np45ag | Torfaen | Tor-Faen | Pantygasseg WwTW | 3869 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328765 | 198644 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AH | NP45AH | np4 5ah | np45ah | Torfaen | Tor-Faen | Pantygasseg WwTW | 4031 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328905 | 198553 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AJ | NP45AJ | np4 5aj | np45aj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4055 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328860 | 198368 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AL | NP45AL | np4 5al | np45al | Torfaen | Tor-Faen | Pantygasseg WwTW | 3927 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328774 | 198497 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AN | NP45AN | np4 5an | np45an | Torfaen | Tor-Faen | Pantygasseg WwTW | 3946 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328715 | 198306 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AP | NP45AP | np4 5ap | np45ap | Torfaen | Tor-Faen | Pantygasseg WwTW | 4034 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328775 | 198225 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AQ | NP45AQ | np4 5aq | np45aq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3785 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328651 | 198575 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AR | NP45AR | np4 5ar | np45ar | Torfaen | Tor-Faen | Pantygasseg WwTW | 4010 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328682 | 198087 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AS | NP45AS | np4 5as | np45as | Torfaen | Tor-Faen | Pantygasseg WwTW | 4031 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328822 | 198338 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AT | NP45AT | np4 5at | np45at | Torfaen | Tor-Faen | Pantygasseg WwTW | 3994 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328857 | 198528 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AU | NP45AU | np4 5au | np45au | Torfaen | Tor-Faen | Pantygasseg WwTW | 3826 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328803 | 198913 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AW | NP45AW | np4 5aw | np45aw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3961 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328664 | 198162 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AX | NP45AX | np4 5ax | np45ax | Torfaen | Tor-Faen | Pantygasseg WwTW | 4025 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328955 | 198724 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AY | NP45AY | np4 5ay | np45ay | Torfaen | Tor-Faen | Pantygasseg WwTW | 3946 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328896 | 198801 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5AZ | NP45AZ | np4 5az | np45az | Torfaen | Tor-Faen | Pantygasseg WwTW | 3870 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328826 | 198833 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BA | NP45BA | np4 5ba | np45ba | Torfaen | Tor-Faen | Pantygasseg WwTW | 3873 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328853 | 198917 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BB | NP45BB | np4 5bb | np45bb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3880 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328885 | 199017 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BD | NP45BD | np4 5bd | np45bd | Torfaen | Tor-Faen | Pantygasseg WwTW | 3969 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328950 | 198909 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BE | NP45BE | np4 5be | np45be | Torfaen | Tor-Faen | Pantygasseg WwTW | 4078 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329026 | 198776 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BG | NP45BG | np4 5bg | np45bg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4265 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329145 | 198532 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BH | NP45BH | np4 5bh | np45bh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4381 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329208 | 198362 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BJ | NP45BJ | np4 5bj | np45bj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4381 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329156 | 198232 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BL | NP45BL | np4 5bl | np45bl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4274 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329045 | 198244 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BN | NP45BN | np4 5bn | np45bn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4139 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328919 | 198292 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BP | NP45BP | np4 5bp | np45bp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4128 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328797 | 198053 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BQ | NP45BQ | np4 5bq | np45bq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4400 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329202 | 198293 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BR | NP45BR | np4 5br | np45br | Torfaen | Tor-Faen | Pantygasseg WwTW | 4107 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328809 | 198126 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BS | NP45BS | np4 5bs | np45bs | Torfaen | Tor-Faen | Pantygasseg WwTW | 4076 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328830 | 198245 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BT | NP45BT | np4 5bt | np45bt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4183 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328853 | 198043 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BU | NP45BU | np4 5bu | np45bu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3901 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328589 | 198145 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BW | NP45BW | np4 5bw | np45bw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4204 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328889 | 198068 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BX | NP45BX | np4 5bx | np45bx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3860 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328632 | 198331 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BY | NP45BY | np4 5by | np45by | Torfaen | Tor-Faen | Pantygasseg WwTW | 4010 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328629 | 197987 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5BZ | NP45BZ | np4 5bz | np45bz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4195 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328822 | 197956 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DA | NP45DA | np4 5da | np45da | Torfaen | Tor-Faen | Pantygasseg WwTW | 3822 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328662 | 198501 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DB | NP45DB | np4 5db | np45db | Torfaen | Tor-Faen | Pantygasseg WwTW | 4322 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328974 | 197975 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DD | NP45DD | np4 5dd | np45dd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4370 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329047 | 198014 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DE | NP45DE | np4 5de | np45de | Torfaen | Tor-Faen | Pantygasseg WwTW | 4335 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329298 | 198794 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DF | NP45DF | np4 5df | np45df | Torfaen | Tor-Faen | Pantygasseg WwTW | 4319 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329321 | 198955 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DG | NP45DG | np4 5dg | np45dg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3822 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328929 | 199952 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DH | NP45DH | np4 5dh | np45dh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4183 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329153 | 198842 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DJ | NP45DJ | np4 5dj | np45dj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4239 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329222 | 198885 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DN | NP45DN | np4 5dn | np45dn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4251 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329217 | 198819 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DP | NP45DP | np4 5dp | np45dp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4417 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329349 | 198671 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DQ | NP45DQ | np4 5dq | np45dq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4060 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328530 | 197721 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DR | NP45DR | np4 5dr | np45dr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4438 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329348 | 198596 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DS | NP45DS | np4 5ds | np45ds | Torfaen | Tor-Faen | Pantygasseg WwTW | 4562 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329381 | 198308 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DT | NP45DT | np4 5dt | np45dt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4515 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329393 | 198483 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DU | NP45DU | np4 5du | np45du | Torfaen | Tor-Faen | Pantygasseg WwTW | 4541 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329353 | 198294 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DW | NP45DW | np4 5dw | np45dw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4292 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329260 | 198821 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DX | NP45DX | np4 5dx | np45dx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4466 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329210 | 198141 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DY | NP45DY | np4 5dy | np45dy | Torfaen | Tor-Faen | Pantygasseg WwTW | 4568 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329323 | 198147 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5DZ | NP45DZ | np4 5dz | np45dz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4700 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329438 | 198078 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EA | NP45EA | np4 5ea | np45ea | Torfaen | Tor-Faen | Pantygasseg WwTW | 4562 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329295 | 198096 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EB | NP45EB | np4 5eb | np45eb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4630 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329358 | 198069 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5ED | NP45ED | np4 5ed | np45ed | Torfaen | Tor-Faen | Pantygasseg WwTW | 4454 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329139 | 198013 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EE | NP45EE | np4 5ee | np45ee | Torfaen | Tor-Faen | Pantygasseg WwTW | 4535 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329229 | 198013 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EF | NP45EF | np4 5ef | np45ef | Torfaen | Tor-Faen | Pantygasseg WwTW | 4693 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329375 | 197954 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EG | NP45EG | np4 5eg | np45eg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4546 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329217 | 197962 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EH | NP45EH | np4 5eh | np45eh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4686 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329402 | 198030 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EJ | NP45EJ | np4 5ej | np45ej | Torfaen | Tor-Faen | Pantygasseg WwTW | 4795 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329482 | 197942 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EL | NP45EL | np4 5el | np45el | Torfaen | Tor-Faen | Pantygasseg WwTW | 4882 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 329541 | 197861 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EN | NP45EN | np4 5en | np45en | Torfaen | Tor-Faen | Pantygasseg WwTW | 4857 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 329539 | 197918 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EP | NP45EP | np4 5ep | np45ep | Torfaen | Tor-Faen | Pantygasseg WwTW | 4637 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329425 | 198215 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EQ | NP45EQ | np4 5eq | np45eq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4581 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329243 | 197935 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5ER | NP45ER | np4 5er | np45er | Torfaen | Tor-Faen | Pantygasseg WwTW | 4641 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 329503 | 198415 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5ES | NP45ES | np4 5es | np45es | Torfaen | Tor-Faen | Pantygasseg WwTW | 4702 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 329508 | 198250 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5ET | NP45ET | np4 5et | np45et | Torfaen | Tor-Faen | Pantygasseg WwTW | 4738 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329454 | 198019 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EU | NP45EU | np4 5eu | np45eu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4641 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329447 | 198261 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EW | NP45EW | np4 5ew | np45ew | Torfaen | Tor-Faen | Pantygasseg WwTW | 4693 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329476 | 198191 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EX | NP45EX | np4 5ex | np45ex | Torfaen | Tor-Faen | Pantygasseg WwTW | 3812 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328729 | 198716 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EY | NP45EY | np4 5ey | np45ey | Torfaen | Tor-Faen | Pantygasseg WwTW | 3746 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328662 | 198723 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5EZ | NP45EZ | np4 5ez | np45ez | Torfaen | Tor-Faen | Pantygasseg WwTW | 3724 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328661 | 198789 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5FA | NP45FA | np4 5fa | np45fa | Torfaen | Tor-Faen | Pantygasseg WwTW | 4450 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329277 | 198349 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5FB | NP45FB | np4 5fb | np45fb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4272 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328958 | 198056 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5FD | NP45FD | np4 5fd | np45fd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4227 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328920 | 198080 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5FH | NP45FH | np4 5fh | np45fh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4731 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 329620 | 198483 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5GZ | NP45GZ | np4 5gz | np45gz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4581 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329480 | 198539 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HA | NP45HA | np4 5ha | np45ha | Torfaen | Tor-Faen | Pantygasseg WwTW | 4038 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329119 | 199438 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HB | NP45HB | np4 5hb | np45hb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4071 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329137 | 199323 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HD | NP45HD | np4 5hd | np45hd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4057 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329071 | 199038 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HE | NP45HE | np4 5he | np45he | Torfaen | Tor-Faen | Pantygasseg WwTW | 3965 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329054 | 199521 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HF | NP45HF | np4 5hf | np45hf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4211 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329294 | 199452 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HG | NP45HG | np4 5hg | np45hg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4103 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329151 | 199211 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HH | NP45HH | np4 5hh | np45hh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4064 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329096 | 199127 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HJ | NP45HJ | np4 5hj | np45hj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4015 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329051 | 199150 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HL | NP45HL | np4 5hl | np45hl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4006 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329031 | 199094 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HN | NP45HN | np4 5hn | np45hn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4093 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329092 | 198970 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HP | NP45HP | np4 5hp | np45hp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4200 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329200 | 198961 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HQ | NP45HQ | np4 5hq | np45hq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4124 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329157 | 199125 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HR | NP45HR | np4 5hr | np45hr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4253 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329254 | 198961 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HS | NP45HS | np4 5hs | np45hs | Torfaen | Tor-Faen | Pantygasseg WwTW | 4202 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329234 | 199113 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HT | NP45HT | np4 5ht | np45ht | Torfaen | Tor-Faen | Pantygasseg WwTW | 4170 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329192 | 199065 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HU | NP45HU | np4 5hu | np45hu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4139 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329197 | 199264 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HW | NP45HW | np4 5hw | np45hw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4158 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329159 | 198970 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HX | NP45HX | np4 5hx | np45hx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4107 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329182 | 199388 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HY | NP45HY | np4 5hy | np45hy | Torfaen | Tor-Faen | Pantygasseg WwTW | 4184 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329216 | 199113 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5HZ | NP45HZ | np4 5hz | np45hz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4165 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329213 | 199204 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JA | NP45JA | np4 5ja | np45ja | Torfaen | Tor-Faen | Pantygasseg WwTW | 4132 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329206 | 199379 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JB | NP45JB | np4 5jb | np45jb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4185 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329260 | 199382 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JD | NP45JD | np4 5jd | np45jd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4198 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329251 | 199233 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JE | NP45JE | np4 5je | np45je | Torfaen | Tor-Faen | Pantygasseg WwTW | 4232 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329276 | 199176 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JF | NP45JF | np4 5jf | np45jf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4303 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329315 | 199001 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JG | NP45JG | np4 5jg | np45jg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4378 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329377 | 198936 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JH | NP45JH | np4 5jh | np45jh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4394 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329398 | 198958 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JJ | NP45JJ | np4 5jj | np45jj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4307 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329356 | 199197 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JL | NP45JL | np4 5jl | np45jl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4245 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329317 | 199355 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JN | NP45JN | np4 5jn | np45jn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4058 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329119 | 199289 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JP | NP45JP | np4 5jp | np45jp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4391 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329380 | 198893 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JQ | NP45JQ | np4 5jq | np45jq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4475 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329489 | 198997 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JR | NP45JR | np4 5jr | np45jr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4502 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329425 | 198629 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JS | NP45JS | np4 5js | np45js | Torfaen | Tor-Faen | Pantygasseg WwTW | 3430 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328503 | 200391 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JT | NP45JT | np4 5jt | np45jt | Torfaen | Tor-Faen | Pantygasseg WwTW | 3574 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328645 | 200418 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JU | NP45JU | np4 5ju | np45ju | Torfaen | Tor-Faen | Pantygasseg WwTW | 3633 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328710 | 200378 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JW | NP45JW | np4 5jw | np45jw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4234 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329298 | 199302 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JX | NP45JX | np4 5jx | np45jx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3632 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328714 | 200337 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JY | NP45JY | np4 5jy | np45jy | Torfaen | Tor-Faen | Pantygasseg WwTW | 3481 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328557 | 200374 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5JZ | NP45JZ | np4 5jz | np45jz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3473 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328563 | 200258 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LA | NP45LA | np4 5la | np45la | Torfaen | Tor-Faen | Pantygasseg WwTW | 3561 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328652 | 200247 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LB | NP45LB | np4 5lb | np45lb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3684 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328766 | 200337 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LD | NP45LD | np4 5ld | np45ld | Torfaen | Tor-Faen | Pantygasseg WwTW | 3872 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328970 | 200181 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LE | NP45LE | np4 5le | np45le | Torfaen | Tor-Faen | Pantygasseg WwTW | 3859 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328948 | 200283 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LF | NP45LF | np4 5lf | np45lf | Torfaen | Tor-Faen | Pantygasseg WwTW | 3941 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329039 | 200178 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LG | NP45LG | np4 5lg | np45lg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3887 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328995 | 199935 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LH | NP45LH | np4 5lh | np45lh | Torfaen | Tor-Faen | Pantygasseg WwTW | 3890 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328993 | 200102 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LJ | NP45LJ | np4 5lj | np45lj | Torfaen | Tor-Faen | Pantygasseg WwTW | 3886 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328986 | 199660 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LL | NP45LL | np4 5ll | np45ll | Torfaen | Tor-Faen | Pantygasseg WwTW | 3874 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328964 | 199530 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LN | NP45LN | np4 5ln | np45ln | Torfaen | Tor-Faen | Pantygasseg WwTW | 3858 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328915 | 199283 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LP | NP45LP | np4 5lp | np45lp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3834 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328913 | 199436 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LQ | NP45LQ | np4 5lq | np45lq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3892 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328997 | 199752 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LR | NP45LR | np4 5lr | np45lr | Torfaen | Tor-Faen | Pantygasseg WwTW | 3865 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328879 | 199057 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LS | NP45LS | np4 5ls | np45ls | Torfaen | Tor-Faen | Pantygasseg WwTW | 3770 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328803 | 199158 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LT | NP45LT | np4 5lt | np45lt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4004 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329010 | 199008 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LU | NP45LU | np4 5lu | np45lu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4441 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329399 | 198761 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LW | NP45LW | np4 5lw | np45lw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3776 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328829 | 199265 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LX | NP45LX | np4 5lx | np45lx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4394 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329442 | 199185 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5LY | NP45LY | np4 5ly | np45ly | Torfaen | Tor-Faen | Pantygasseg WwTW | 4035 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328989 | 198802 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5NA | NP45NA | np4 5na | np45na | Torfaen | Tor-Faen | Pantygasseg WwTW | 4614 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329393 | 198196 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5NB | NP45NB | np4 5nb | np45nb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3970 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329076 | 200036 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5NE | NP45NE | np4 5ne | np45ne | Torfaen | Tor-Faen | Pantygasseg WwTW | 4204 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 329222 | 199042 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5PD | NP45PD | np4 5pd | np45pd | Torfaen | Tor-Faen | Pantygasseg WwTW | 3487 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328589 | 200098 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5QU | NP45QU | np4 5qu | np45qu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3778 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328878 | 199670 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5RR | NP45RR | np4 5rr | np45rr | Torfaen | Tor-Faen | Pantygasseg WwTW | 2906 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328013 | 199961 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5RS | NP45RS | np4 5rs | np45rs | Torfaen | Tor-Faen | Pantygasseg WwTW | 2760 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327868 | 199891 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5RT | NP45RT | np4 5rt | np45rt | Torfaen | Tor-Faen | Pantygasseg WwTW | 2811 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327919 | 199943 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5RU | NP45RU | np4 5ru | np45ru | Torfaen | Tor-Faen | Pantygasseg WwTW | 3023 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328125 | 200089 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5RX | NP45RX | np4 5rx | np45rx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3388 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328482 | 200207 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5RY | NP45RY | np4 5ry | np45ry | Torfaen | Tor-Faen | Pantygasseg WwTW | 3142 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328242 | 200128 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5RZ | NP45RZ | np4 5rz | np45rz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3359 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328450 | 200243 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SA | NP45SA | np4 5sa | np45sa | Torfaen | Tor-Faen | Pantygasseg WwTW | 3275 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328374 | 200149 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SB | NP45SB | np4 5sb | np45sb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3335 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328438 | 200085 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SD | NP45SD | np4 5sd | np45sd | Torfaen | Tor-Faen | Pantygasseg WwTW | 3380 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328486 | 200030 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SE | NP45SE | np4 5se | np45se | Torfaen | Tor-Faen | Pantygasseg WwTW | 3225 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328333 | 199929 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SF | NP45SF | np4 5sf | np45sf | Torfaen | Tor-Faen | Pantygasseg WwTW | 3032 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328140 | 199943 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SG | NP45SG | np4 5sg | np45sg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3079 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328186 | 199816 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SH | NP45SH | np4 5sh | np45sh | Torfaen | Tor-Faen | Pantygasseg WwTW | 3186 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328291 | 200038 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SJ | NP45SJ | np4 5sj | np45sj | Torfaen | Tor-Faen | Pantygasseg WwTW | 2931 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328039 | 199896 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SL | NP45SL | np4 5sl | np45sl | Torfaen | Tor-Faen | Pantygasseg WwTW | 3455 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328560 | 200034 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SN | NP45SN | np4 5sn | np45sn | Torfaen | Tor-Faen | Pantygasseg WwTW | 3513 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328612 | 200150 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SP | NP45SP | np4 5sp | np45sp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3600 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328693 | 200233 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SQ | NP45SQ | np4 5sq | np45sq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3293 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328401 | 199893 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SS | NP45SS | np4 5ss | np45ss | Torfaen | Tor-Faen | Pantygasseg WwTW | 3824 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328928 | 200077 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5ST | NP45ST | np4 5st | np45st | Torfaen | Tor-Faen | Pantygasseg WwTW | 3842 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328756 | 198702 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SU | NP45SU | np4 5su | np45su | Torfaen | Tor-Faen | Pantygasseg WwTW | 3811 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328912 | 199675 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SW | NP45SW | np4 5sw | np45sw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3373 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328471 | 200158 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SX | NP45SX | np4 5sx | np45sx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4661 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329602 | 198669 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SY | NP45SY | np4 5sy | np45sy | Torfaen | Tor-Faen | Pantygasseg WwTW | 4602 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329583 | 198832 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5SZ | NP45SZ | np4 5sz | np45sz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3428 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328528 | 200140 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5UF | NP45UF | np4 5uf | np45uf | Torfaen | Tor-Faen | Pantygasseg WwTW | 2519 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327625 | 200009 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5UG | NP45UG | np4 5ug | np45ug | Torfaen | Tor-Faen | Pantygasseg WwTW | 2554 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327659 | 200039 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5UH | NP45UH | np4 5uh | np45uh | Torfaen | Tor-Faen | Pantygasseg WwTW | 2354 | 1568 | Over1500 | 3.14 | 2.3 | 1.68 | 29.23 | 15.59 | 17.23 | 327445 | 200186 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5UY | NP45UY | np4 5uy | np45uy | Torfaen | Tor-Faen | Pantygasseg WwTW | 2437 | 1606 | Over1500 | 3.21 | 2.35 | 1.72 | 29.93 | 15.96 | 17.64 | 327489 | 199384 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5UZ | NP45UZ | np4 5uz | np45uz | Torfaen | Tor-Faen | Pantygasseg WwTW | 2566 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 327613 | 199350 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XB | NP45XB | np4 5xb | np45xb | Torfaen | Tor-Faen | Pantygasseg WwTW | 2492 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 327556 | 199436 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XE | NP45XE | np4 5xe | np45xe | Torfaen | Tor-Faen | Pantygasseg WwTW | 2578 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327655 | 199503 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XF | NP45XF | np4 5xf | np45xf | Torfaen | Tor-Faen | Pantygasseg WwTW | 2201 | 1606 | Over1500 | 3.21 | 2.35 | 1.72 | 29.93 | 15.96 | 17.64 | 327264 | 199463 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XG | NP45XG | np4 5xg | np45xg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3723 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328817 | 200228 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XJ | NP45XJ | np4 5xj | np45xj | Torfaen | Tor-Faen | Pantygasseg WwTW | 3273 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 328264 | 199040 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XN | NP45XN | np4 5xn | np45xn | Torfaen | Tor-Faen | Pantygasseg WwTW | 3233 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 328245 | 199125 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XP | NP45XP | np4 5xp | np45xp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3494 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 328536 | 199229 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XQ | NP45XQ | np4 5xq | np45xq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3050 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 328052 | 199107 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XS | NP45XS | np4 5xs | np45xs | Torfaen | Tor-Faen | Pantygasseg WwTW | 3014 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328102 | 199562 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XU | NP45XU | np4 5xu | np45xu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3271 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 328198 | 198833 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XW | NP45XW | np4 5xw | np45xw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3235 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 328244 | 199112 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XX | NP45XX | np4 5xx | np45xx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3289 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 328162 | 198684 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XY | NP45XY | np4 5xy | np45xy | Torfaen | Tor-Faen | Pantygasseg WwTW | 3480 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 328354 | 198651 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5XZ | NP45XZ | np4 5xz | np45xz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3447 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 328217 | 198418 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5YA | NP45YA | np4 5ya | np45ya | Torfaen | Tor-Faen | Pantygasseg WwTW | 4075 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329170 | 199584 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5YE | NP45YE | np4 5ye | np45ye | Torfaen | Tor-Faen | Pantygasseg WwTW | 2847 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327951 | 200051 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5YG | NP45YG | np4 5yg | np45yg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3290 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328378 | 200262 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5YH | NP45YH | np4 5yh | np45yh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4982 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 329674 | 197914 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5YJ | NP45YJ | np4 5yj | np45yj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4869 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 329604 | 198037 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5YL | NP45YL | np4 5yl | np45yl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4836 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 329635 | 198206 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5YN | NP45YN | np4 5yn | np45yn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4916 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 329688 | 198121 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 5ZA | NP45ZA | np4 5za | np45za | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AA | NP46AA | np4 6aa | np46aa | Torfaen | Tor-Faen | Pantygasseg WwTW | 2986 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328020 | 200566 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AB | NP46AB | np4 6ab | np46ab | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326782 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AD | NP46AD | np4 6ad | np46ad | Torfaen | Tor-Faen | Pantygasseg WwTW | 2459 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326859 | 201631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AE | NP46AE | np4 6ae | np46ae | Torfaen | Tor-Faen | Pantygasseg WwTW | 2964 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327991 | 200592 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AF | NP46AF | np4 6af | np46af | Torfaen | Tor-Faen | Pantygasseg WwTW | 2638 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327622 | 200704 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AG | NP46AG | np4 6ag | np46ag | Torfaen | Tor-Faen | Pantygasseg WwTW | 2554 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327587 | 200521 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AH | NP46AH | np4 6ah | np46ah | Torfaen | Tor-Faen | Pantygasseg WwTW | 2661 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327549 | 200965 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AJ | NP46AJ | np4 6aj | np46aj | Torfaen | Tor-Faen | Pantygasseg WwTW | 2954 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327973 | 200624 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AL | NP46AL | np4 6al | np46al | Torfaen | Tor-Faen | Pantygasseg WwTW | 2883 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327912 | 200574 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AN | NP46AN | np4 6an | np46an | Torfaen | Tor-Faen | Pantygasseg WwTW | 2541 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327498 | 200769 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AP | NP46AP | np4 6ap | np46ap | Torfaen | Tor-Faen | Pantygasseg WwTW | 2831 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327864 | 200551 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AQ | NP46AQ | np4 6aq | np46aq | Torfaen | Tor-Faen | Pantygasseg WwTW | 2595 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327597 | 200639 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AR | NP46AR | np4 6ar | np46ar | Torfaen | Tor-Faen | Pantygasseg WwTW | 2660 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327714 | 200439 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AS | NP46AS | np4 6as | np46as | Torfaen | Tor-Faen | Pantygasseg WwTW | 2633 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327678 | 200477 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AT | NP46AT | np4 6at | np46at | Torfaen | Tor-Faen | Pantygasseg WwTW | 2512 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327570 | 200406 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AU | NP46AU | np4 6au | np46au | Torfaen | Tor-Faen | Pantygasseg WwTW | 2619 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327649 | 200539 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AW | NP46AW | np4 6aw | np46aw | Torfaen | Tor-Faen | Pantygasseg WwTW | 2405 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327357 | 200758 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AX | NP46AX | np4 6ax | np46ax | Torfaen | Tor-Faen | Pantygasseg WwTW | 2532 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327462 | 200837 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AY | NP46AY | np4 6ay | np46ay | Torfaen | Tor-Faen | Pantygasseg WwTW | 2261 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327205 | 200752 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6AZ | NP46AZ | np4 6az | np46az | Torfaen | Tor-Faen | Pantygasseg WwTW | 2031 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 326954 | 200752 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BA | NP46BA | np4 6ba | np46ba | Torfaen | Tor-Faen | Pantygasseg WwTW | 2289 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327270 | 200656 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BB | NP46BB | np4 6bb | np46bb | Torfaen | Tor-Faen | Pantygasseg WwTW | 2393 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327374 | 200676 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BD | NP46BD | np4 6bd | np46bd | Torfaen | Tor-Faen | Pantygasseg WwTW | 2386 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327358 | 200698 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BE | NP46BE | np4 6be | np46be | Torfaen | Tor-Faen | Pantygasseg WwTW | 2335 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327268 | 200793 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BG | NP46BG | np4 6bg | np46bg | Torfaen | Tor-Faen | Pantygasseg WwTW | 2215 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327138 | 200791 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BH | NP46BH | np4 6bh | np46bh | Torfaen | Tor-Faen | Pantygasseg WwTW | 2313 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327233 | 200820 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BL | NP46BL | np4 6bl | np46bl | Torfaen | Tor-Faen | Pantygasseg WwTW | 2398 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327213 | 201053 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BN | NP46BN | np4 6bn | np46bn | Torfaen | Tor-Faen | Pantygasseg WwTW | 2245 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327146 | 200848 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BP | NP46BP | np4 6bp | np46bp | Torfaen | Tor-Faen | Pantygasseg WwTW | 1922 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 326807 | 200804 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BQ | NP46BQ | np4 6bq | np46bq | Torfaen | Tor-Faen | Pantygasseg WwTW | 2149 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327070 | 200783 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BR | NP46BR | np4 6br | np46br | Torfaen | Tor-Faen | Pantygasseg WwTW | 3042 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327945 | 201002 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BS | NP46BS | np4 6bs | np46bs | Torfaen | Tor-Faen | Pantygasseg WwTW | 2208 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327178 | 200674 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BT | NP46BT | np4 6bt | np46bt | Torfaen | Tor-Faen | Pantygasseg WwTW | 2528 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327502 | 200716 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BU | NP46BU | np4 6bu | np46bu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3150 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328032 | 201077 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BW | NP46BW | np4 6bw | np46bw | Torfaen | Tor-Faen | Pantygasseg WwTW | 2322 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327209 | 200895 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BX | NP46BX | np4 6bx | np46bx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3060 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327844 | 201276 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BY | NP46BY | np4 6by | np46by | Torfaen | Tor-Faen | Pantygasseg WwTW | 3149 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328013 | 201121 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6BZ | NP46BZ | np4 6bz | np46bz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3137 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328014 | 201087 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DA | NP46DA | np4 6da | np46da | Torfaen | Tor-Faen | Pantygasseg WwTW | 3226 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328002 | 201329 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DB | NP46DB | np4 6db | np46db | Torfaen | Tor-Faen | Pantygasseg WwTW | 3029 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327795 | 201302 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DD | NP46DD | np4 6dd | np46dd | Torfaen | Tor-Faen | Pantygasseg WwTW | 3064 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327854 | 201263 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DE | NP46DE | np4 6de | np46de | Torfaen | Tor-Faen | Pantygasseg WwTW | 2990 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327630 | 201510 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DF | NP46DF | np4 6df | np46df | Torfaen | Tor-Faen | Pantygasseg WwTW | 3044 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327733 | 201446 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DG | NP46DG | np4 6dg | np46dg | Torfaen | Tor-Faen | Pantygasseg WwTW | 2933 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327644 | 201379 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DH | NP46DH | np4 6dh | np46dh | Torfaen | Tor-Faen | Pantygasseg WwTW | 3224 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328041 | 201244 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DJ | NP46DJ | np4 6dj | np46dj | Torfaen | Tor-Faen | Pantygasseg WwTW | 2712 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327479 | 201222 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DL | NP46DL | np4 6dl | np46dl | Torfaen | Tor-Faen | Pantygasseg WwTW | 2992 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327713 | 201376 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DN | NP46DN | np4 6dn | np46dn | Torfaen | Tor-Faen | Pantygasseg WwTW | 2913 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327519 | 201540 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DP | NP46DP | np4 6dp | np46dp | Torfaen | Tor-Faen | Pantygasseg WwTW | 2758 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327493 | 201290 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DQ | NP46DQ | np4 6dq | np46dq | Torfaen | Tor-Faen | Pantygasseg WwTW | 2852 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327574 | 201337 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DR | NP46DR | np4 6dr | np46dr | Torfaen | Tor-Faen | Pantygasseg WwTW | 2904 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327436 | 201640 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DS | NP46DS | np4 6ds | np46ds | Torfaen | Tor-Faen | Pantygasseg WwTW | 2970 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327566 | 201572 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DT | NP46DT | np4 6dt | np46dt | Torfaen | Tor-Faen | Pantygasseg WwTW | 2914 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327563 | 201475 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DU | NP46DU | np4 6du | np46du | Torfaen | Tor-Faen | Pantygasseg WwTW | 2804 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327452 | 201443 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DW | NP46DW | np4 6dw | np46dw | Torfaen | Tor-Faen | Pantygasseg WwTW | 2841 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327433 | 201537 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DX | NP46DX | np4 6dx | np46dx | Torfaen | Tor-Faen | Pantygasseg WwTW | 2867 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327537 | 201428 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DY | NP46DY | np4 6dy | np46dy | Torfaen | Tor-Faen | Pantygasseg WwTW | 2684 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327415 | 201276 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6DZ | NP46DZ | np4 6dz | np46dz | Torfaen | Tor-Faen | Pantygasseg WwTW | 2740 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327423 | 201370 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EA | NP46EA | np4 6ea | np46ea | Torfaen | Tor-Faen | Pantygasseg WwTW | 2795 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327488 | 201371 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EB | NP46EB | np4 6eb | np46eb | Torfaen | Tor-Faen | Pantygasseg WwTW | 2595 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327334 | 201239 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6ED | NP46ED | np4 6ed | np46ed | Torfaen | Tor-Faen | Pantygasseg WwTW | 2598 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327393 | 201141 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EE | NP46EE | np4 6ee | np46ee | Torfaen | Tor-Faen | Pantygasseg WwTW | 2646 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327395 | 201236 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EF | NP46EF | np4 6ef | np46ef | Torfaen | Tor-Faen | Pantygasseg WwTW | 2702 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327495 | 201172 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EG | NP46EG | np4 6eg | np46eg | Torfaen | Tor-Faen | Pantygasseg WwTW | 2556 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327370 | 201096 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EH | NP46EH | np4 6eh | np46eh | Torfaen | Tor-Faen | Pantygasseg WwTW | 2837 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327590 | 201279 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EJ | NP46EJ | np4 6ej | np46ej | Torfaen | Tor-Faen | Pantygasseg WwTW | 2885 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327462 | 201572 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EL | NP46EL | np4 6el | np46el | Torfaen | Tor-Faen | Pantygasseg WwTW | 2651 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327355 | 201311 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EN | NP46EN | np4 6en | np46en | Torfaen | Tor-Faen | Pantygasseg WwTW | 2870 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327894 | 200596 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EP | NP46EP | np4 6ep | np46ep | Torfaen | Tor-Faen | Pantygasseg WwTW | 2764 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327787 | 200587 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EQ | NP46EQ | np4 6eq | np46eq | Torfaen | Tor-Faen | Pantygasseg WwTW | 2668 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327457 | 201170 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6ER | NP46ER | np4 6er | np46er | Torfaen | Tor-Faen | Pantygasseg WwTW | 192 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 325300 | 199883 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6ES | NP46ES | np4 6es | np46es | Torfaen | Tor-Faen | Pantygasseg WwTW | 2569 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327466 | 200926 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6ET | NP46ET | np4 6et | np46et | Torfaen | Tor-Faen | Pantygasseg WwTW | 2827 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327840 | 200633 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EU | NP46EU | np4 6eu | np46eu | Torfaen | Tor-Faen | Pantygasseg WwTW | 2716 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327713 | 200672 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EW | NP46EW | np4 6ew | np46ew | Torfaen | Tor-Faen | Pantygasseg WwTW | 3328 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328347 | 200667 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EX | NP46EX | np4 6ex | np46ex | Torfaen | Tor-Faen | Pantygasseg WwTW | 2819 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327824 | 200661 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EY | NP46EY | np4 6ey | np46ey | Torfaen | Tor-Faen | Pantygasseg WwTW | 3025 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328024 | 200709 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6EZ | NP46EZ | np4 6ez | np46ez | Torfaen | Tor-Faen | Pantygasseg WwTW | 2940 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327950 | 200657 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6FA | NP46FA | np4 6fa | np46fa | Torfaen | Tor-Faen | Pantygasseg WwTW | 2064 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 327014 | 200698 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6FD | NP46FD | np4 6fd | np46fd | Torfaen | Tor-Faen | Pantygasseg WwTW | 2933 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327818 | 201027 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6GE | NP46GE | np4 6ge | np46ge | Torfaen | Tor-Faen | Pantygasseg WwTW | 2831 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327881 | 200476 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6GP | NP46GP | np4 6gp | np46gp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3274 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328014 | 201413 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6GS | NP46GS | np4 6gs | np46gs | Torfaen | Tor-Faen | Pantygasseg WwTW | 3247 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327929 | 201512 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6GT | NP46GT | np4 6gt | np46gt | Torfaen | Tor-Faen | Pantygasseg WwTW | 3231 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327947 | 201447 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HA | NP46HA | np4 6ha | np46ha | Torfaen | Tor-Faen | Pantygasseg WwTW | 2737 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327721 | 200719 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HB | NP46HB | np4 6hb | np46hb | Torfaen | Tor-Faen | Pantygasseg WwTW | 2832 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327824 | 200709 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HD | NP46HD | np4 6hd | np46hd | Torfaen | Tor-Faen | Pantygasseg WwTW | 2716 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327624 | 200927 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HE | NP46HE | np4 6he | np46he | Torfaen | Tor-Faen | Pantygasseg WwTW | 2643 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327616 | 200739 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HF | NP46HF | np4 6hf | np46hf | Torfaen | Tor-Faen | Pantygasseg WwTW | 2695 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327648 | 200805 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HG | NP46HG | np4 6hg | np46hg | Torfaen | Tor-Faen | Pantygasseg WwTW | 2858 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327821 | 200804 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HH | NP46HH | np4 6hh | np46hh | Torfaen | Tor-Faen | Pantygasseg WwTW | 2800 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327723 | 200905 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HJ | NP46HJ | np4 6hj | np46hj | Torfaen | Tor-Faen | Pantygasseg WwTW | 2806 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327758 | 200827 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HL | NP46HL | np4 6hl | np46hl | Torfaen | Tor-Faen | Pantygasseg WwTW | 2914 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327730 | 201176 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HN | NP46HN | np4 6hn | np46hn | Torfaen | Tor-Faen | Pantygasseg WwTW | 3016 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327887 | 201078 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HP | NP46HP | np4 6hp | np46hp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3004 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327838 | 201158 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HQ | NP46HQ | np4 6hq | np46hq | Torfaen | Tor-Faen | Pantygasseg WwTW | 2925 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327892 | 200803 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HR | NP46HR | np4 6hr | np46hr | Torfaen | Tor-Faen | Pantygasseg WwTW | 2962 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327811 | 201115 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HS | NP46HS | np4 6hs | np46hs | Torfaen | Tor-Faen | Pantygasseg WwTW | 2876 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327717 | 201115 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HT | NP46HT | np4 6ht | np46ht | Torfaen | Tor-Faen | Pantygasseg WwTW | 2845 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327732 | 201004 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HU | NP46HU | np4 6hu | np46hu | Torfaen | Tor-Faen | Pantygasseg WwTW | 2924 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327858 | 200899 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HW | NP46HW | np4 6hw | np46hw | Torfaen | Tor-Faen | Pantygasseg WwTW | 2970 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327926 | 200843 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6HX | NP46HX | np4 6hx | np46hx | Torfaen | Tor-Faen | Pantygasseg WwTW | 2840 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327795 | 200824 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JA | NP46JA | np4 6ja | np46ja | Torfaen | Tor-Faen | Pantygasseg WwTW | 2765 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327094 | 201829 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JB | NP46JB | np4 6jb | np46jb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3282 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328094 | 201267 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JD | NP46JD | np4 6jd | np46jd | Torfaen | Tor-Faen | Pantygasseg WwTW | 3215 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328099 | 201085 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JE | NP46JE | np4 6je | np46je | Torfaen | Tor-Faen | Pantygasseg WwTW | 3285 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328190 | 201040 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JF | NP46JF | np4 6jf | np46jf | Torfaen | Tor-Faen | Pantygasseg WwTW | 3334 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328199 | 201155 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JG | NP46JG | np4 6jg | np46jg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3265 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328149 | 201092 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JH | NP46JH | np4 6jh | np46jh | Torfaen | Tor-Faen | Pantygasseg WwTW | 3405 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328311 | 201060 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JJ | NP46JJ | np4 6jj | np46jj | Torfaen | Tor-Faen | Pantygasseg WwTW | 3233 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328157 | 200980 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JL | NP46JL | np4 6jl | np46jl | Torfaen | Tor-Faen | Pantygasseg WwTW | 3250 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328230 | 200808 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JN | NP46JN | np4 6jn | np46jn | Torfaen | Tor-Faen | Pantygasseg WwTW | 3196 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328146 | 200897 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JQ | NP46JQ | np4 6jq | np46jq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3265 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328217 | 200903 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JR | NP46JR | np4 6jr | np46jr | Torfaen | Tor-Faen | Pantygasseg WwTW | 3289 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328197 | 201033 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JS | NP46JS | np4 6js | np46js | Torfaen | Tor-Faen | Pantygasseg WwTW | 3231 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328178 | 200913 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JT | NP46JT | np4 6jt | np46jt | Torfaen | Tor-Faen | Pantygasseg WwTW | 3241 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328244 | 200721 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JU | NP46JU | np4 6ju | np46ju | Torfaen | Tor-Faen | Pantygasseg WwTW | 3261 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328289 | 200623 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JW | NP46JW | np4 6jw | np46jw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3192 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328130 | 200931 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JX | NP46JX | np4 6jx | np46jx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3093 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328092 | 200719 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JY | NP46JY | np4 6jy | np46jy | Torfaen | Tor-Faen | Pantygasseg WwTW | 3057 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328066 | 200677 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6JZ | NP46JZ | np4 6jz | np46jz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3047 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328069 | 200622 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LA | NP46LA | np4 6la | np46la | Torfaen | Tor-Faen | Pantygasseg WwTW | 3073 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328103 | 200591 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LB | NP46LB | np4 6lb | np46lb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3126 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328158 | 200588 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LD | NP46LD | np4 6ld | np46ld | Torfaen | Tor-Faen | Pantygasseg WwTW | 2796 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327837 | 200513 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LE | NP46LE | np4 6le | np46le | Torfaen | Tor-Faen | Pantygasseg WwTW | 3084 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328125 | 200545 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LF | NP46LF | np4 6lf | np46lf | Torfaen | Tor-Faen | Pantygasseg WwTW | 2934 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327974 | 200532 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LG | NP46LG | np4 6lg | np46lg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3303 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328337 | 200600 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LH | NP46LH | np4 6lh | np46lh | Torfaen | Tor-Faen | Pantygasseg WwTW | 2690 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327736 | 200481 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LJ | NP46LJ | np4 6lj | np46lj | Torfaen | Tor-Faen | Pantygasseg WwTW | 2864 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327905 | 200520 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LL | NP46LL | np4 6ll | np46ll | Torfaen | Tor-Faen | Pantygasseg WwTW | 3313 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328327 | 200689 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LN | NP46LN | np4 6ln | np46ln | Torfaen | Tor-Faen | Pantygasseg WwTW | 2991 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328009 | 200635 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LP | NP46LP | np4 6lp | np46lp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3110 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328131 | 200637 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LQ | NP46LQ | np4 6lq | np46lq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3271 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328318 | 200533 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LR | NP46LR | np4 6lr | np46lr | Torfaen | Tor-Faen | Pantygasseg WwTW | 3188 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328094 | 201021 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LS | NP46LS | np4 6ls | np46ls | Torfaen | Tor-Faen | Pantygasseg WwTW | 3141 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327953 | 201235 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LT | NP46LT | np4 6lt | np46lt | Torfaen | Tor-Faen | Pantygasseg WwTW | 3195 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328062 | 201121 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LU | NP46LU | np4 6lu | np46lu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3177 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327961 | 201302 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LW | NP46LW | np4 6lw | np46lw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3254 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328287 | 200598 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LX | NP46LX | np4 6lx | np46lx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3165 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327889 | 201416 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LY | NP46LY | np4 6ly | np46ly | Torfaen | Tor-Faen | Pantygasseg WwTW | 3121 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328076 | 200870 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6LZ | NP46LZ | np4 6lz | np46lz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3196 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327911 | 201441 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NA | NP46NA | np4 6na | np46na | Torfaen | Tor-Faen | Pantygasseg WwTW | 3156 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328112 | 200871 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NB | NP46NB | np4 6nb | np46nb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3190 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328129 | 200930 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6ND | NP46ND | np4 6nd | np46nd | Torfaen | Tor-Faen | Pantygasseg WwTW | 3190 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328109 | 200986 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NE | NP46NE | np4 6ne | np46ne | Torfaen | Tor-Faen | Pantygasseg WwTW | 2968 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327452 | 201725 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NF | NP46NF | np4 6nf | np46nf | Torfaen | Tor-Faen | Pantygasseg WwTW | 3001 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327445 | 201788 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NG | NP46NG | np4 6ng | np46ng | Torfaen | Tor-Faen | Pantygasseg WwTW | 3065 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327446 | 201887 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NH | NP46NH | np4 6nh | np46nh | Torfaen | Tor-Faen | Pantygasseg WwTW | 3159 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328099 | 200920 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NL | NP46NL | np4 6nl | np46nl | Torfaen | Tor-Faen | Pantygasseg WwTW | 3013 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327375 | 201890 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NN | NP46NN | np4 6nn | np46nn | Torfaen | Tor-Faen | Pantygasseg WwTW | 3164 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328026 | 201129 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NQ | NP46NQ | np4 6nq | np46nq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3148 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327853 | 201446 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PF | NP441PF | np44 1pf | np441pf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4583 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329432 | 195698 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PG | NP441PG | np44 1pg | np441pg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4759 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329320 | 196207 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PH | NP441PH | np44 1ph | np441ph | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4823 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329245 | 196148 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PL | NP441PL | np44 1pl | np441pl | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4505 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329499 | 195506 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PN | NP441PN | np44 1pn | np441pn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4524 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329484 | 195582 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PP | NP441PP | np44 1pp | np441pp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4557 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329453 | 195625 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PQ | NP441PQ | np44 1pq | np441pq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4487 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329515 | 195435 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PR | NP441PR | np44 1pr | np441pr | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4584 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329425 | 195617 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PS | NP441PS | np44 1ps | np441ps | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4554 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329448 | 195438 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PT | NP441PT | np44 1pt | np441pt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4617 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329386 | 195445 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PU | NP441PU | np44 1pu | np441pu | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4570 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329432 | 195399 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PW | NP441PW | np44 1pw | np441pw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4587 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329418 | 195517 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PX | NP441PX | np44 1px | np441px | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4506 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329496 | 195363 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PY | NP441PY | np44 1py | np441py | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4606 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329411 | 195724 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NR | NP46NR | np4 6nr | np46nr | Torfaen | Tor-Faen | Pantygasseg WwTW | 3084 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327673 | 201617 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NS | NP46NS | np4 6ns | np46ns | Torfaen | Tor-Faen | Pantygasseg WwTW | 3121 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327723 | 201608 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NT | NP46NT | np4 6nt | np46nt | Torfaen | Tor-Faen | Pantygasseg WwTW | 3107 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327725 | 201579 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NU | NP46NU | np4 6nu | np46nu | Torfaen | Tor-Faen | Pantygasseg WwTW | 2973 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327481 | 201696 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NW | NP46NW | np4 6nw | np46nw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3157 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327968 | 201242 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NY | NP46NY | np4 6ny | np46ny | Torfaen | Tor-Faen | Pantygasseg WwTW | 3104 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327540 | 201833 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6NZ | NP46NZ | np4 6nz | np46nz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3273 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328126 | 201170 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PA | NP46PA | np4 6pa | np46pa | Torfaen | Tor-Faen | Pantygasseg WwTW | 2649 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326883 | 201871 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PB | NP46PB | np4 6pb | np46pb | Torfaen | Tor-Faen | Pantygasseg WwTW | 2868 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327341 | 201704 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PD | NP46PD | np4 6pd | np46pd | Torfaen | Tor-Faen | Pantygasseg WwTW | 2929 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327284 | 201865 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PE | NP46PE | np4 6pe | np46pe | Torfaen | Tor-Faen | Pantygasseg WwTW | 2876 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327237 | 201838 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PF | NP46PF | np4 6pf | np46pf | Torfaen | Tor-Faen | Pantygasseg WwTW | 2805 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327155 | 201822 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PG | NP46PG | np4 6pg | np46pg | Torfaen | Tor-Faen | Pantygasseg WwTW | 2716 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327100 | 201751 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PH | NP46PH | np4 6ph | np46ph | Torfaen | Tor-Faen | Pantygasseg WwTW | 2675 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327031 | 201764 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PJ | NP46PJ | np4 6pj | np46pj | Torfaen | Tor-Faen | Pantygasseg WwTW | 2593 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326966 | 201713 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PL | NP46PL | np4 6pl | np46pl | Torfaen | Tor-Faen | Pantygasseg WwTW | 2671 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327054 | 201734 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PN | NP46PN | np4 6pn | np46pn | Torfaen | Tor-Faen | Pantygasseg WwTW | 2602 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326928 | 201765 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PP | NP46PP | np4 6pp | np46pp | Torfaen | Tor-Faen | Pantygasseg WwTW | 2682 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327012 | 201794 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PQ | NP46PQ | np4 6pq | np46pq | Torfaen | Tor-Faen | Pantygasseg WwTW | 2257 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 326491 | 201688 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PR | NP46PR | np4 6pr | np46pr | Torfaen | Tor-Faen | Pantygasseg WwTW | 2696 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326983 | 201842 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PS | NP46PS | np4 6ps | np46ps | Torfaen | Tor-Faen | Pantygasseg WwTW | 2705 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326939 | 201896 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PT | NP46PT | np4 6pt | np46pt | Torfaen | Tor-Faen | Pantygasseg WwTW | 2685 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326904 | 201901 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PU | NP46PU | np4 6pu | np46pu | Torfaen | Tor-Faen | Pantygasseg WwTW | 2669 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326862 | 201917 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PW | NP46PW | np4 6pw | np46pw | Torfaen | Tor-Faen | Pantygasseg WwTW | 2626 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326960 | 201766 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PX | NP46PX | np4 6px | np46px | Torfaen | Tor-Faen | Pantygasseg WwTW | 2666 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326889 | 201889 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PY | NP46PY | np4 6py | np46py | Torfaen | Tor-Faen | Pantygasseg WwTW | 2682 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326848 | 201946 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6PZ | NP46PZ | np4 6pz | np46pz | Torfaen | Tor-Faen | Pantygasseg WwTW | 2644 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326853 | 201891 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QA | NP46QA | np4 6qa | np46qa | Torfaen | Tor-Faen | Pantygasseg WwTW | 2155 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326517 | 201536 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QB | NP46QB | np4 6qb | np46qb | Torfaen | Tor-Faen | Pantygasseg WwTW | 2411 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326709 | 201707 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QD | NP46QD | np4 6qd | np46qd | Torfaen | Tor-Faen | Pantygasseg WwTW | 2218 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326602 | 201544 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QE | NP46QE | np4 6qe | np46qe | Torfaen | Tor-Faen | Pantygasseg WwTW | 2617 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326895 | 201817 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QF | NP46QF | np4 6qf | np46qf | Torfaen | Tor-Faen | Pantygasseg WwTW | 2643 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326929 | 201821 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QG | NP46QG | np4 6qg | np46qg | Torfaen | Tor-Faen | Pantygasseg WwTW | 2576 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326891 | 201764 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QH | NP46QH | np4 6qh | np46qh | Torfaen | Tor-Faen | Pantygasseg WwTW | 1906 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 326329 | 201368 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QJ | NP46QJ | np4 6qj | np46qj | Torfaen | Tor-Faen | Pantygasseg WwTW | 1851 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 326284 | 201334 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QL | NP46QL | np4 6ql | np46ql | Torfaen | Tor-Faen | Pantygasseg WwTW | 2224 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326588 | 201565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QN | NP46QN | np4 6qn | np46qn | Torfaen | Tor-Faen | Pantygasseg WwTW | 2436 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326748 | 201706 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QP | NP46QP | np4 6qp | np46qp | Torfaen | Tor-Faen | Pantygasseg WwTW | 2122 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 326487 | 201518 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QQ | NP46QQ | np4 6qq | np46qq | Torfaen | Tor-Faen | Pantygasseg WwTW | 2521 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326841 | 201736 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QR | NP46QR | np4 6qr | np46qr | Torfaen | Tor-Faen | Pantygasseg WwTW | 2439 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326704 | 201749 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QS | NP46QS | np4 6qs | np46qs | Torfaen | Tor-Faen | Pantygasseg WwTW | 2613 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326784 | 201910 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QT | NP46QT | np4 6qt | np46qt | Torfaen | Tor-Faen | Pantygasseg WwTW | 2249 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 326251 | 201842 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QU | NP46QU | np4 6qu | np46qu | Torfaen | Tor-Faen | Pantygasseg WwTW | 2637 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326795 | 201932 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QW | NP46QW | np4 6qw | np46qw | Torfaen | Tor-Faen | Pantygasseg WwTW | 2767 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327144 | 201778 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QX | NP46QX | np4 6qx | np46qx | Torfaen | Tor-Faen | Pantygasseg WwTW | 2429 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326681 | 201756 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QY | NP46QY | np4 6qy | np46qy | Torfaen | Tor-Faen | Pantygasseg WwTW | 2494 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326663 | 201854 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6QZ | NP46QZ | np4 6qz | np46qz | Torfaen | Tor-Faen | Pantygasseg WwTW | 2511 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326614 | 201914 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RA | NP46RA | np4 6ra | np46ra | Torfaen | Tor-Faen | Pantygasseg WwTW | 2668 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326791 | 201975 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RB | NP46RB | np4 6rb | np46rb | Torfaen | Tor-Faen | Pantygasseg WwTW | 2623 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326743 | 201956 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RD | NP46RD | np4 6rd | np46rd | Torfaen | Tor-Faen | Pantygasseg WwTW | 2724 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326817 | 202026 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RE | NP46RE | np4 6re | np46re | Torfaen | Tor-Faen | Pantygasseg WwTW | 2656 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326815 | 201939 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RF | NP46RF | np4 6rf | np46rf | Torfaen | Tor-Faen | Pantygasseg WwTW | 2617 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326756 | 201937 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RG | NP46RG | np4 6rg | np46rg | Torfaen | Tor-Faen | Pantygasseg WwTW | 2717 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326783 | 202044 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RH | NP46RH | np4 6rh | np46rh | Torfaen | Tor-Faen | Pantygasseg WwTW | 2607 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326815 | 201875 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RJ | NP46RJ | np4 6rj | np46rj | Torfaen | Tor-Faen | Pantygasseg WwTW | 2689 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326575 | 202158 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RL | NP46RL | np4 6rl | np46rl | Torfaen | Tor-Faen | Pantygasseg WwTW | 2820 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326940 | 202049 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RN | NP46RN | np4 6rn | np46rn | Torfaen | Tor-Faen | Pantygasseg WwTW | 2741 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326650 | 202171 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RP | NP46RP | np4 6rp | np46rp | Torfaen | Tor-Faen | Pantygasseg WwTW | 2695 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326644 | 202119 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RQ | NP46RQ | np4 6rq | np46rq | Torfaen | Tor-Faen | Pantygasseg WwTW | 2664 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326737 | 202013 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RR | NP46RR | np4 6rr | np46rr | Torfaen | Tor-Faen | Pantygasseg WwTW | 2816 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326740 | 202200 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RS | NP46RS | np4 6rs | np46rs | Torfaen | Tor-Faen | Pantygasseg WwTW | 2777 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326878 | 202044 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RT | NP46RT | np4 6rt | np46rt | Torfaen | Tor-Faen | Pantygasseg WwTW | 2864 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326920 | 202123 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RU | NP46RU | np4 6ru | np46ru | Torfaen | Tor-Faen | Pantygasseg WwTW | 2823 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327034 | 201969 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RW | NP46RW | np4 6rw | np46rw | Torfaen | Tor-Faen | Pantygasseg WwTW | 2705 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326683 | 202104 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RX | NP46RX | np4 6rx | np46rx | Torfaen | Tor-Faen | Pantygasseg WwTW | 2853 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327050 | 201994 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RY | NP46RY | np4 6ry | np46ry | Torfaen | Tor-Faen | Pantygasseg WwTW | 2679 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326760 | 202014 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6RZ | NP46RZ | np4 6rz | np46rz | Torfaen | Tor-Faen | Pantygasseg WwTW | 2798 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326828 | 202111 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SA | NP46SA | np4 6sa | np46sa | Torfaen | Tor-Faen | Pantygasseg WwTW | 2886 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327161 | 201933 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SB | NP46SB | np4 6sb | np46sb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3927 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327039 | 203323 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SD | NP46SD | np4 6sd | np46sd | Torfaen | Tor-Faen | Pantygasseg WwTW | 3031 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327064 | 202220 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SE | NP46SE | np4 6se | np46se | Torfaen | Tor-Faen | Pantygasseg WwTW | 2808 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327074 | 201910 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SF | NP46SF | np4 6sf | np46sf | Torfaen | Tor-Faen | Pantygasseg WwTW | 2771 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327075 | 201857 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SG | NP46SG | np4 6sg | np46sg | Torfaen | Tor-Faen | Pantygasseg WwTW | 2889 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327107 | 201991 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SH | NP46SH | np4 6sh | np46sh | Torfaen | Tor-Faen | Pantygasseg WwTW | 2961 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327034 | 202153 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SJ | NP46SJ | np4 6sj | np46sj | Torfaen | Tor-Faen | Pantygasseg WwTW | 2982 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327064 | 202156 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SL | NP46SL | np4 6sl | np46sl | Torfaen | Tor-Faen | Pantygasseg WwTW | 2966 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327096 | 202106 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SN | NP46SN | np4 6sn | np46sn | Torfaen | Tor-Faen | Pantygasseg WwTW | 2928 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327103 | 202048 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SP | NP46SP | np4 6sp | np46sp | Torfaen | Tor-Faen | Pantygasseg WwTW | 2952 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327126 | 202059 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SQ | NP46SQ | np4 6sq | np46sq | Torfaen | Tor-Faen | Pantygasseg WwTW | 2885 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327054 | 202035 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SR | NP46SR | np4 6sr | np46sr | Torfaen | Tor-Faen | Pantygasseg WwTW | 2935 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327165 | 201998 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SS | NP46SS | np4 6ss | np46ss | Torfaen | Tor-Faen | Pantygasseg WwTW | 2898 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327210 | 201899 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6ST | NP46ST | np4 6st | np46st | Torfaen | Tor-Faen | Pantygasseg WwTW | 2931 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327244 | 201911 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SU | NP46SU | np4 6su | np46su | Torfaen | Tor-Faen | Pantygasseg WwTW | 2960 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327253 | 201944 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SW | NP46SW | np4 6sw | np46sw | Torfaen | Tor-Faen | Pantygasseg WwTW | 2941 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327077 | 202089 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SX | NP46SX | np4 6sx | np46sx | Torfaen | Tor-Faen | Pantygasseg WwTW | 2964 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327193 | 202011 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SY | NP46SY | np4 6sy | np46sy | Torfaen | Tor-Faen | Pantygasseg WwTW | 3018 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327090 | 202180 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6SZ | NP46SZ | np4 6sz | np46sz | Torfaen | Tor-Faen | Pantygasseg WwTW | 2992 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327138 | 202102 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TA | NP46TA | np4 6ta | np46ta | Torfaen | Tor-Faen | Pantygasseg WwTW | 3145 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326920 | 202475 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TB | NP46TB | np4 6tb | np46tb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3401 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326997 | 202732 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TD | NP46TD | np4 6td | np46td | Torfaen | Tor-Faen | Pantygasseg WwTW | 4047 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327129 | 203410 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TE | NP46TE | np4 6te | np46te | Torfaen | Tor-Faen | Pantygasseg WwTW | 3469 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327010 | 202805 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TF | NP46TF | np4 6tf | np46tf | Torfaen | Tor-Faen | Pantygasseg WwTW | 3569 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327028 | 202913 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TG | NP46TG | np4 6tg | np46tg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4006 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327058 | 203403 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TH | NP46TH | np4 6th | np46th | Torfaen | Tor-Faen | Pantygasseg WwTW | 4152 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 327133 | 203529 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TJ | NP46TJ | np4 6tj | np46tj | Torfaen | Tor-Faen | Pantygasseg WwTW | 2830 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326695 | 202248 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TL | NP46TL | np4 6tl | np46tl | Torfaen | Tor-Faen | Pantygasseg WwTW | 3652 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327031 | 203009 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TN | NP46TN | np4 6tn | np46tn | Torfaen | Tor-Faen | Pantygasseg WwTW | 2234 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326502 | 201651 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TP | NP46TP | np4 6tp | np46tp | Torfaen | Tor-Faen | Pantygasseg WwTW | 2167 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 326637 | 201441 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TQ | NP46TQ | np4 6tq | np46tq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4029 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327075 | 203420 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TR | NP46TR | np4 6tr | np46tr | Torfaen | Tor-Faen | Pantygasseg WwTW | 2066 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 325761 | 201865 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TS | NP46TS | np4 6ts | np46ts | Torfaen | Tor-Faen | Pantygasseg WwTW | 2868 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326856 | 202178 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TT | NP46TT | np4 6tt | np46tt | Torfaen | Tor-Faen | Pantygasseg WwTW | 1468 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 325970 | 201093 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TU | NP46TU | np4 6tu | np46tu | Torfaen | Tor-Faen | Pantygasseg WwTW | 1798 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 326249 | 201294 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TW | NP46TW | np4 6tw | np46tw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3192 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326906 | 202542 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TX | NP46TX | np4 6tx | np46tx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3276 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326959 | 202607 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TY | NP46TY | np4 6ty | np46ty | Torfaen | Tor-Faen | Pantygasseg WwTW | 149 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 325062 | 199764 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6TZ | NP46TZ | np4 6tz | np46tz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3076 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326929 | 202384 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UA | NP46UA | np4 6ua | np46ua | Torfaen | Tor-Faen | Pantygasseg WwTW | 727 | 1535 | Over1500 | 3.07 | 2.25 | 1.65 | 28.61 | 15.26 | 16.86 | 324432 | 199641 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UB | NP46UB | np4 6ub | np46ub | Torfaen | Tor-Faen | Pantygasseg WwTW | 1546 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 325856 | 201258 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UD | NP46UD | np4 6ud | np46ud | Torfaen | Tor-Faen | Pantygasseg WwTW | 165 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 325267 | 199857 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UE | NP46UE | np4 6ue | np46ue | Torfaen | Tor-Faen | Pantygasseg WwTW | 702 | 1569 | Over1500 | 3.14 | 2.3 | 1.69 | 29.24 | 15.6 | 17.24 | 325537 | 200461 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UF | NP46UF | np4 6uf | np46uf | Torfaen | Tor-Faen | Pantygasseg WwTW | 1607 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 326123 | 201151 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UH | NP46UH | np4 6uh | np46uh | Torfaen | Tor-Faen | Pantygasseg WwTW | 121 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 325157 | 199794 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UJ | NP46UJ | np4 6uj | np46uj | Torfaen | Tor-Faen | Pantygasseg WwTW | 1045 | 1535 | Over1500 | 3.07 | 2.25 | 1.65 | 28.61 | 15.26 | 16.86 | 324177 | 200376 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UL | NP46UL | np4 6ul | np46ul | Torfaen | Tor-Faen | Pantygasseg WwTW | 1013 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 325602 | 200789 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UN | NP46UN | np4 6un | np46un | Torfaen | Tor-Faen | Pantygasseg WwTW | 1330 | 1554 | Over1500 | 3.11 | 2.28 | 1.67 | 28.96 | 15.45 | 17.07 | 324981 | 201228 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UP | NP46UP | np4 6up | np46up | Torfaen | Tor-Faen | Pantygasseg WwTW | 2147 | 1568 | Over1500 | 3.14 | 2.3 | 1.68 | 29.23 | 15.59 | 17.23 | 327188 | 200438 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UR | NP46UR | np4 6ur | np46ur | Torfaen | Tor-Faen | Pantygasseg WwTW | 1793 | 1568 | Over1500 | 3.14 | 2.3 | 1.68 | 29.23 | 15.59 | 17.23 | 326843 | 200359 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6US | NP46US | np4 6us | np46us | Torfaen | Tor-Faen | Pantygasseg WwTW | 1141 | 1569 | Over1500 | 3.14 | 2.3 | 1.69 | 29.24 | 15.6 | 17.24 | 326226 | 200138 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UT | NP46UT | np4 6ut | np46ut | Torfaen | Tor-Faen | Pantygasseg WwTW | 1774 | 1568 | Over1500 | 3.14 | 2.3 | 1.68 | 29.23 | 15.59 | 17.23 | 326813 | 200396 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UU | NP46UU | np4 6uu | np46uu | Torfaen | Tor-Faen | Pantygasseg WwTW | 1757 | 1568 | Over1500 | 3.14 | 2.3 | 1.68 | 29.23 | 15.59 | 17.23 | 326803 | 200369 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6UW | NP46UW | np4 6uw | np46uw | Torfaen | Tor-Faen | Pantygasseg WwTW | 2580 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 326933 | 201728 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6WD | NP46WD | np4 6wd | np46wd | Torfaen | Tor-Faen | Pantygasseg WwTW | 2964 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327216 | 201988 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6XA | NP46XA | np4 6xa | np46xa | Torfaen | Tor-Faen | Pantygasseg WwTW | 3210 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328091 | 201090 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6XG | NP46XG | np4 6xg | np46xg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3368 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328305 | 200965 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6XP | NP46XP | np4 6xp | np46xp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3265 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328317 | 200508 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6XQ | NP46XQ | np4 6xq | np46xq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3300 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328155 | 201172 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6XT | NP46XT | np4 6xt | np46xt | Torfaen | Tor-Faen | Pantygasseg WwTW | 3255 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328196 | 200933 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6XU | NP46XU | np4 6xu | np46xu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3230 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328146 | 201002 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6XY | NP46XY | np4 6xy | np46xy | Torfaen | Tor-Faen | Pantygasseg WwTW | 3244 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328208 | 200859 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6YB | NP46YB | np4 6yb | np46yb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3228 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328215 | 200779 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6YN | NP46YN | np4 6yn | np46yn | Torfaen | Tor-Faen | Pantygasseg WwTW | 3173 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328139 | 200842 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6YW | NP46YW | np4 6yw | np46yw | Torfaen | Tor-Faen | Pantygasseg WwTW | 2684 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327129 | 201671 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 6ZE | NP46ZE | np4 6ze | np46ze | Torfaen | Tor-Faen | Pantygasseg WwTW | 3228 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328215 | 200779 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AA | NP47AA | np4 7aa | np47aa | Torfaen | Tor-Faen | Pantygasseg WwTW | 3792 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 326321 | 203497 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AB | NP47AB | np4 7ab | np47ab | Torfaen | Tor-Faen | Pantygasseg WwTW | 3828 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 326479 | 203478 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AD | NP47AD | np4 7ad | np47ad | Torfaen | Tor-Faen | Pantygasseg WwTW | 3872 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326607 | 203474 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AE | NP47AE | np4 7ae | np47ae | Torfaen | Tor-Faen | Pantygasseg WwTW | 3838 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326680 | 203405 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AF | NP47AF | np4 7af | np47af | Torfaen | Tor-Faen | Pantygasseg WwTW | 3864 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326803 | 203376 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AG | NP47AG | np4 7ag | np47ag | Torfaen | Tor-Faen | Pantygasseg WwTW | 3866 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326885 | 203337 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AH | NP47AH | np4 7ah | np47ah | Torfaen | Tor-Faen | Pantygasseg WwTW | 3846 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326468 | 203501 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AJ | NP47AJ | np4 7aj | np47aj | Torfaen | Tor-Faen | Pantygasseg WwTW | 3822 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 326458 | 203480 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AL | NP47AL | np4 7al | np47al | Torfaen | Tor-Faen | Pantygasseg WwTW | 3951 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326677 | 203530 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AN | NP47AN | np4 7an | np47an | Torfaen | Tor-Faen | Pantygasseg WwTW | 3996 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326692 | 203573 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AP | NP47AP | np4 7ap | np47ap | Torfaen | Tor-Faen | Pantygasseg WwTW | 4398 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326438 | 204096 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AQ | NP47AQ | np4 7aq | np47aq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3833 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326721 | 203381 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AR | NP47AR | np4 7ar | np47ar | Torfaen | Tor-Faen | Pantygasseg WwTW | 3932 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326598 | 203543 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AS | NP47AS | np4 7as | np47as | Torfaen | Tor-Faen | Pantygasseg WwTW | 3915 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326165 | 203674 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AT | NP47AT | np4 7at | np47at | Torfaen | Tor-Faen | Pantygasseg WwTW | 5336 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326474 | 205062 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AU | NP47AU | np4 7au | np47au | Torfaen | Tor-Faen | Pantygasseg WwTW | 3916 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326566 | 203539 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AW | NP47AW | np4 7aw | np47aw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3931 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326679 | 203507 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7AZ | NP47AZ | np4 7az | np47az | Torfaen | Tor-Faen | Pantygasseg WwTW | 3891 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326578 | 203507 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BA | NP47BA | np4 7ba | np47ba | Torfaen | Tor-Faen | Pantygasseg WwTW | 3770 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327022 | 203152 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BB | NP47BB | np4 7bb | np47bb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3789 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326606 | 203384 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BD | NP47BD | np4 7bd | np47bd | Torfaen | Tor-Faen | Pantygasseg WwTW | 5192 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 326512 | 204902 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BE | NP47BE | np4 7be | np47be | Torfaen | Tor-Faen | Pantygasseg WwTW | 3904 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326759 | 203442 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BG | NP47BG | np4 7bg | np47bg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3915 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326814 | 203428 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BH | NP47BH | np4 7bh | np47bh | Torfaen | Tor-Faen | Pantygasseg WwTW | 3838 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327009 | 203238 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BJ | NP47BJ | np4 7bj | np47bj | Torfaen | Tor-Faen | Pantygasseg WwTW | 3582 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326945 | 202979 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BL | NP47BL | np4 7bl | np47bl | Torfaen | Tor-Faen | Pantygasseg WwTW | 3478 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326871 | 202902 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BN | NP47BN | np4 7bn | np47bn | Torfaen | Tor-Faen | Pantygasseg WwTW | 3610 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326845 | 203069 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BP | NP47BP | np4 7bp | np47bp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3532 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326867 | 202967 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BQ | NP47BQ | np4 7bq | np47bq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3846 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326966 | 203272 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BR | NP47BR | np4 7br | np47br | Torfaen | Tor-Faen | Pantygasseg WwTW | 3521 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326904 | 202933 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BS | NP47BS | np4 7bs | np47bs | Torfaen | Tor-Faen | Pantygasseg WwTW | 3602 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326926 | 203014 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BT | NP47BT | np4 7bt | np47bt | Torfaen | Tor-Faen | Pantygasseg WwTW | 3652 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326958 | 203053 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BU | NP47BU | np4 7bu | np47bu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3447 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326925 | 202834 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BW | NP47BW | np4 7bw | np47bw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3450 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326792 | 202915 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BX | NP47BX | np4 7bx | np47bx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3448 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326902 | 202849 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BY | NP47BY | np4 7by | np47by | Torfaen | Tor-Faen | Pantygasseg WwTW | 3322 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326898 | 202703 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7BZ | NP47BZ | np4 7bz | np47bz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3306 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326823 | 202731 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DA | NP47DA | np4 7da | np47da | Torfaen | Tor-Faen | Pantygasseg WwTW | 3731 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326864 | 203196 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DB | NP47DB | np4 7db | np47db | Torfaen | Tor-Faen | Pantygasseg WwTW | 3931 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325521 | 203813 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DF | NP47DF | np4 7df | np47df | Torfaen | Tor-Faen | Pantygasseg WwTW | 4353 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326953 | 203847 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DG | NP47DG | np4 7dg | np47dg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3928 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326905 | 203397 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DH | NP47DH | np4 7dh | np47dh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4023 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326680 | 203607 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DJ | NP47DJ | np4 7dj | np47dj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4066 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326710 | 203641 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DL | NP47DL | np4 7dl | np47dl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4163 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326741 | 203733 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DN | NP47DN | np4 7dn | np47dn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4295 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326748 | 203873 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DP | NP47DP | np4 7dp | np47dp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4260 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326747 | 203836 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DQ | NP47DQ | np4 7dq | np47dq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4063 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326829 | 203584 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DR | NP47DR | np4 7dr | np47dr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4261 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326665 | 203870 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DS | NP47DS | np4 7ds | np47ds | Torfaen | Tor-Faen | Pantygasseg WwTW | 4150 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326706 | 203734 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DT | NP47DT | np4 7dt | np47dt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4040 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326594 | 203661 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DU | NP47DU | np4 7du | np47du | Torfaen | Tor-Faen | Pantygasseg WwTW | 4036 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326620 | 203646 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DW | NP47DW | np4 7dw | np47dw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4345 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326583 | 203991 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DX | NP47DX | np4 7dx | np47dx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4075 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326654 | 203674 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DY | NP47DY | np4 7dy | np47dy | Torfaen | Tor-Faen | Pantygasseg WwTW | 3938 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326522 | 203579 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7DZ | NP47DZ | np4 7dz | np47dz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3939 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326485 | 203594 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7EA | NP47EA | np4 7ea | np47ea | Torfaen | Tor-Faen | Pantygasseg WwTW | 3878 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326264 | 203606 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7EB | NP47EB | np4 7eb | np47eb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3929 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326278 | 203655 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7ED | NP47ED | np4 7ed | np47ed | Torfaen | Tor-Faen | Pantygasseg WwTW | 3870 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326075 | 203651 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7EE | NP47EE | np4 7ee | np47ee | Torfaen | Tor-Faen | Pantygasseg WwTW | 4092 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326162 | 203858 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7EF | NP47EF | np4 7ef | np47ef | Torfaen | Tor-Faen | Pantygasseg WwTW | 3832 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326148 | 203592 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7EG | NP47EG | np4 7eg | np47eg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3737 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 326478 | 203381 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7EJ | NP47EJ | np4 7ej | np47ej | Torfaen | Tor-Faen | Pantygasseg WwTW | 4649 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326074 | 204451 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7EL | NP47EL | np4 7el | np47el | Torfaen | Tor-Faen | Pantygasseg WwTW | 3727 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 326436 | 203386 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7EP | NP47EP | np4 7ep | np47ep | Torfaen | Tor-Faen | Pantygasseg WwTW | 3749 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326598 | 203344 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7EQ | NP47EQ | np4 7eq | np47eq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3996 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326091 | 203777 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7EU | NP47EU | np4 7eu | np47eu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4109 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326119 | 203887 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7EW | NP47EW | np4 7ew | np47ew | Torfaen | Tor-Faen | Pantygasseg WwTW | 3856 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326933 | 203301 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HA | NP47HA | np4 7ha | np47ha | Torfaen | Tor-Faen | Pantygasseg WwTW | 4002 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326290 | 203727 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HB | NP47HB | np4 7hb | np47hb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3954 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326383 | 203647 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HD | NP47HD | np4 7hd | np47hd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4063 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326398 | 203757 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HE | NP47HE | np4 7he | np47he | Torfaen | Tor-Faen | Pantygasseg WwTW | 4073 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326541 | 203717 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HF | NP47HF | np4 7hf | np47hf | Torfaen | Tor-Faen | Pantygasseg WwTW | 3981 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326489 | 203638 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HG | NP47HG | np4 7hg | np47hg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4161 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326563 | 203802 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HH | NP47HH | np4 7hh | np47hh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4078 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326436 | 203760 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HJ | NP47HJ | np4 7hj | np47hj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4140 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326501 | 203803 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HL | NP47HL | np4 7hl | np47hl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4167 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326504 | 203830 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HN | NP47HN | np4 7hn | np47hn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4179 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326449 | 203862 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HP | NP47HP | np4 7hp | np47hp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4150 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326369 | 203858 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HQ | NP47HQ | np4 7hq | np47hq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4198 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326565 | 203841 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HR | NP47HR | np4 7hr | np47hr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4233 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326342 | 203953 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HS | NP47HS | np4 7hs | np47hs | Torfaen | Tor-Faen | Pantygasseg WwTW | 4220 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326392 | 203924 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HT | NP47HT | np4 7ht | np47ht | Torfaen | Tor-Faen | Pantygasseg WwTW | 4208 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326266 | 203949 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HU | NP47HU | np4 7hu | np47hu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4278 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326264 | 204023 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HW | NP47HW | np4 7hw | np47hw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4198 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326342 | 203916 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HX | NP47HX | np4 7hx | np47hx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4294 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326110 | 204079 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HY | NP47HY | np4 7hy | np47hy | Torfaen | Tor-Faen | Pantygasseg WwTW | 4536 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326056 | 204339 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7HZ | NP47HZ | np4 7hz | np47hz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4529 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326082 | 204327 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JA | NP47JA | np4 7ja | np47ja | Torfaen | Tor-Faen | Pantygasseg WwTW | 4383 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326125 | 204167 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JB | NP47JB | np4 7jb | np47jb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4407 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326172 | 204180 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JD | NP47JD | np4 7jd | np47jd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4349 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326167 | 204122 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JE | NP47JE | np4 7je | np47je | Torfaen | Tor-Faen | Pantygasseg WwTW | 4653 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326177 | 204432 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JF | NP47JF | np4 7jf | np47jf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4635 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326199 | 204408 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JG | NP47JG | np4 7jg | np47jg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4373 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326238 | 204128 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JH | NP47JH | np4 7jh | np47jh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4436 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326042 | 204240 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JJ | NP47JJ | np4 7jj | np47jj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4698 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326165 | 204481 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JL | NP47JL | np4 7jl | np47jl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4500 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326208 | 204267 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JN | NP47JN | np4 7jn | np47jn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4381 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326369 | 204099 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JP | NP47JP | np4 7jp | np47jp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4428 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326263 | 204178 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JQ | NP47JQ | np4 7jq | np47jq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4413 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326279 | 204159 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JR | NP47JR | np4 7jr | np47jr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4393 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326297 | 204133 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JS | NP47JS | np4 7js | np47js | Torfaen | Tor-Faen | Pantygasseg WwTW | 4285 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326306 | 204018 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JT | NP47JT | np4 7jt | np47jt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4333 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326357 | 204053 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JU | NP47JU | np4 7ju | np47ju | Torfaen | Tor-Faen | Pantygasseg WwTW | 4363 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326293 | 204103 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JW | NP47JW | np4 7jw | np47jw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4345 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326346 | 204069 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JX | NP47JX | np4 7jx | np47jx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4469 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326204 | 204236 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JY | NP47JY | np4 7jy | np47jy | Torfaen | Tor-Faen | Pantygasseg WwTW | 4343 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326188 | 204110 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7JZ | NP47JZ | np4 7jz | np47jz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4251 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326105 | 204036 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LA | NP47LA | np4 7la | np47la | Torfaen | Tor-Faen | Pantygasseg WwTW | 4185 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326206 | 203942 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LB | NP47LB | np4 7lb | np47lb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4122 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326274 | 203858 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LD | NP47LD | np4 7ld | np47ld | Torfaen | Tor-Faen | Pantygasseg WwTW | 4440 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326121 | 204227 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LE | NP47LE | np4 7le | np47le | Torfaen | Tor-Faen | Pantygasseg WwTW | 4111 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326509 | 203769 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LH | NP47LH | np4 7lh | np47lh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4935 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326341 | 204682 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LJ | NP47LJ | np4 7lj | np47lj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4962 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326288 | 204723 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LL | NP47LL | np4 7ll | np47ll | Torfaen | Tor-Faen | Pantygasseg WwTW | 5064 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326388 | 204803 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LP | NP47LP | np4 7lp | np47lp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4988 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326460 | 204705 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LR | NP47LR | np4 7lr | np47lr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4935 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326488 | 204642 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LS | NP47LS | np4 7ls | np47ls | Torfaen | Tor-Faen | Pantygasseg WwTW | 4875 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 326659 | 204525 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LT | NP47LT | np4 7lt | np47lt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4945 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 326622 | 204611 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LU | NP47LU | np4 7lu | np47lu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4802 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326620 | 204461 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LW | NP47LW | np4 7lw | np47lw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4959 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326498 | 204664 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LX | NP47LX | np4 7lx | np47lx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4763 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326646 | 204411 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LY | NP47LY | np4 7ly | np47ly | Torfaen | Tor-Faen | Pantygasseg WwTW | 4773 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326556 | 204452 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7LZ | NP47LZ | np4 7lz | np47lz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4861 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326449 | 204576 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7NA | NP47NA | np4 7na | np47na | Torfaen | Tor-Faen | Pantygasseg WwTW | 4840 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 326520 | 204533 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7NH | NP47NH | np4 7nh | np47nh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4723 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326437 | 204436 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7NL | NP47NL | np4 7nl | np47nl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4716 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326388 | 204443 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7NN | NP47NN | np4 7nn | np47nn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4624 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326343 | 204360 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7NP | NP47NP | np4 7np | np47np | Torfaen | Tor-Faen | Pantygasseg WwTW | 4741 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326319 | 204487 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7NQ | NP47NQ | np4 7nq | np47nq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4810 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326342 | 204553 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7NR | NP47NR | np4 7nr | np47nr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4748 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326213 | 204521 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7NU | NP47NU | np4 7nu | np47nu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4635 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326289 | 204386 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7NW | NP47NW | np4 7nw | np47nw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4530 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326399 | 204246 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7NY | NP47NY | np4 7ny | np47ny | Torfaen | Tor-Faen | Pantygasseg WwTW | 4515 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326431 | 204221 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7NZ | NP47NZ | np4 7nz | np47nz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4503 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326440 | 204205 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PA | NP47PA | np4 7pa | np47pa | Torfaen | Tor-Faen | Pantygasseg WwTW | 4475 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326478 | 204164 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PB | NP47PB | np4 7pb | np47pb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4450 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326504 | 204129 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PD | NP47PD | np4 7pd | np47pd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4441 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326528 | 204112 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PE | NP47PE | np4 7pe | np47pe | Torfaen | Tor-Faen | Pantygasseg WwTW | 4450 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326569 | 204107 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PF | NP47PF | np4 7pf | np47pf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4446 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326607 | 204089 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PG | NP47PG | np4 7pg | np47pg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4500 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326670 | 204124 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PH | NP47PH | np4 7ph | np47ph | Torfaen | Tor-Faen | Pantygasseg WwTW | 4641 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326738 | 204249 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PJ | NP47PJ | np4 7pj | np47pj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4477 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326705 | 204086 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PL | NP47PL | np4 7pl | np47pl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4774 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326283 | 204531 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PQ | NP47PQ | np4 7pq | np47pq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4571 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326753 | 204168 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PT | NP47PT | np4 7pt | np47pt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4461 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326716 | 204065 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PU | NP47PU | np4 7pu | np47pu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4445 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326729 | 204043 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PX | NP47PX | np4 7px | np47px | Torfaen | Tor-Faen | Llanellen STW | 6248 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 326543 | 206160 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PY | NP47PY | np4 7py | np47py | Torfaen | Tor-Faen | Pantygasseg WwTW | 5619 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326368 | 205379 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7PZ | NP47PZ | np4 7pz | np47pz | Torfaen | Tor-Faen | Pantygasseg WwTW | 5450 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326298 | 205222 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QA | NP47QA | np4 7qa | np47qa | Torfaen | Tor-Faen | Pantygasseg WwTW | 5174 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326150 | 204971 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QB | NP47QB | np4 7qb | np47qb | Torfaen | Tor-Faen | Pantygasseg WwTW | 5166 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326064 | 204980 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QD | NP47QD | np4 7qd | np47qd | Torfaen | Tor-Faen | Pantygasseg WwTW | 5123 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326159 | 204918 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QE | NP47QE | np4 7qe | np47qe | Torfaen | Tor-Faen | Pantygasseg WwTW | 5440 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326176 | 205237 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QF | NP47QF | np4 7qf | np47qf | Torfaen | Tor-Faen | Pantygasseg WwTW | 5439 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326228 | 205226 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QG | NP47QG | np4 7qg | np47qg | Torfaen | Tor-Faen | Pantygasseg WwTW | 5120 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326118 | 204923 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QH | NP47QH | np4 7qh | np47qh | Torfaen | Tor-Faen | Pantygasseg WwTW | 5240 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326210 | 205026 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QJ | NP47QJ | np4 7qj | np47qj | Torfaen | Tor-Faen | Pantygasseg WwTW | 5038 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326233 | 204814 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QL | NP47QL | np4 7ql | np47ql | Torfaen | Tor-Faen | Pantygasseg WwTW | 5028 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326090 | 204835 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QN | NP47QN | np4 7qn | np47qn | Torfaen | Tor-Faen | Pantygasseg WwTW | 5054 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326326 | 204809 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QQ | NP47QQ | np4 7qq | np47qq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5169 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326192 | 204958 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QR | NP47QR | np4 7qr | np47qr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4910 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326205 | 204689 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QS | NP47QS | np4 7qs | np47qs | Torfaen | Tor-Faen | Pantygasseg WwTW | 4853 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326269 | 204616 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QT | NP47QT | np4 7qt | np47qt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4809 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326249 | 204575 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QU | NP47QU | np4 7qu | np47qu | Torfaen | Tor-Faen | Pantygasseg WwTW | 5029 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326125 | 204829 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QW | NP47QW | np4 7qw | np47qw | Torfaen | Tor-Faen | Pantygasseg WwTW | 5017 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326295 | 204778 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QX | NP47QX | np4 7qx | np47qx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4919 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 325999 | 204741 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QY | NP47QY | np4 7qy | np47qy | Torfaen | Tor-Faen | Pantygasseg WwTW | 4906 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326009 | 204726 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7QZ | NP47QZ | np4 7qz | np47qz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4716 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 325985 | 204537 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RA | NP47RA | np4 7ra | np47ra | Torfaen | Tor-Faen | Pantygasseg WwTW | 4725 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326019 | 204540 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RB | NP47RB | np4 7rb | np47rb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4491 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325920 | 204321 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RD | NP47RD | np4 7rd | np47rd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4682 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326014 | 204497 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RE | NP47RE | np4 7re | np47re | Torfaen | Tor-Faen | Pantygasseg WwTW | 4663 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325998 | 204481 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RF | NP47RF | np4 7rf | np47rf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4674 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 325892 | 204511 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RG | NP47RG | np4 7rg | np47rg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4692 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 326062 | 204498 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RH | NP47RH | np4 7rh | np47rh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4610 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325926 | 204440 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RJ | NP47RJ | np4 7rj | np47rj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4552 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325863 | 204393 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RL | NP47RL | np4 7rl | np47rl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4576 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325917 | 204408 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RP | NP47RP | np4 7rp | np47rp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4880 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326379 | 204615 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RQ | NP47RQ | np4 7rq | np47rq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4645 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325946 | 204472 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RR | NP47RR | np4 7rr | np47rr | Torfaen | Tor-Faen | Pantygasseg WwTW | 5003 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326194 | 204787 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RS | NP47RS | np4 7rs | np47rs | Torfaen | Tor-Faen | Pantygasseg WwTW | 5026 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326161 | 204818 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RT | NP47RT | np4 7rt | np47rt | Torfaen | Tor-Faen | Pantygasseg WwTW | 6154 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 326619 | 205869 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RU | NP47RU | np4 7ru | np47ru | Torfaen | Tor-Faen | Llanellen STW | 5866 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 326788 | 206454 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RW | NP47RW | np4 7rw | np47rw | Torfaen | Tor-Faen | Pantygasseg WwTW | 5833 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 326488 | 205571 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RX | NP47RX | np4 7rx | np47rx | Torfaen | Tor-Faen | Pantygasseg WwTW | 5766 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 326454 | 205510 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RY | NP47RY | np4 7ry | np47ry | Torfaen | Tor-Faen | Pantygasseg WwTW | 5775 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 326572 | 205490 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7RZ | NP47RZ | np4 7rz | np47rz | Torfaen | Tor-Faen | Pantygasseg WwTW | 5678 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 326581 | 205387 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SA | NP47SA | np4 7sa | np47sa | Torfaen | Tor-Faen | Pantygasseg WwTW | 5682 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 326614 | 205382 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SB | NP47SB | np4 7sb | np47sb | Torfaen | Tor-Faen | Pantygasseg WwTW | 5632 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326407 | 205383 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SD | NP47SD | np4 7sd | np47sd | Torfaen | Tor-Faen | Pantygasseg WwTW | 5477 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326380 | 205231 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SE | NP47SE | np4 7se | np47se | Torfaen | Tor-Faen | Pantygasseg WwTW | 5045 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326487 | 204756 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SF | NP47SF | np4 7sf | np47sf | Torfaen | Tor-Faen | Pantygasseg WwTW | 5449 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 326533 | 205163 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SG | NP47SG | np4 7sg | np47sg | Torfaen | Tor-Faen | Pantygasseg WwTW | 5285 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326333 | 205044 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SH | NP47SH | np4 7sh | np47sh | Torfaen | Tor-Faen | Pantygasseg WwTW | 5151 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326252 | 204926 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SJ | NP47SJ | np4 7sj | np47sj | Torfaen | Tor-Faen | Pantygasseg WwTW | 5122 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326445 | 204848 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SN | NP47SN | np4 7sn | np47sn | Torfaen | Tor-Faen | Pantygasseg WwTW | 5088 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 326560 | 204780 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SP | NP47SP | np4 7sp | np47sp | Torfaen | Tor-Faen | Pantygasseg WwTW | 5310 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326418 | 205049 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SQ | NP47SQ | np4 7sq | np47sq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5278 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326453 | 205007 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SR | NP47SR | np4 7sr | np47sr | Torfaen | Tor-Faen | Pantygasseg WwTW | 5451 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326439 | 205189 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SS | NP47SS | np4 7ss | np47ss | Torfaen | Tor-Faen | Pantygasseg WwTW | 5639 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326473 | 205375 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7ST | NP47ST | np4 7st | np47st | Torfaen | Tor-Faen | Pantygasseg WwTW | 5316 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326267 | 205092 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SU | NP47SU | np4 7su | np47su | Torfaen | Tor-Faen | Pantygasseg WwTW | 5364 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326316 | 205130 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SW | NP47SW | np4 7sw | np47sw | Torfaen | Tor-Faen | Pantygasseg WwTW | 5212 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326366 | 204961 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SX | NP47SX | np4 7sx | np47sx | Torfaen | Tor-Faen | Pantygasseg WwTW | 5257 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 326612 | 204941 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7SY | NP47SY | np4 7sy | np47sy | Torfaen | Tor-Faen | Pantygasseg WwTW | 2722 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 326356 | 202323 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TA | NP47TA | np4 7ta | np47ta | Torfaen | Tor-Faen | Pantygasseg WwTW | 2885 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 326474 | 202446 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TB | NP47TB | np4 7tb | np47tb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3011 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326527 | 202560 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TD | NP47TD | np4 7td | np47td | Torfaen | Tor-Faen | Pantygasseg WwTW | 3051 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326531 | 202603 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TE | NP47TE | np4 7te | np47te | Torfaen | Tor-Faen | Pantygasseg WwTW | 3548 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326630 | 203109 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TF | NP47TF | np4 7tf | np47tf | Torfaen | Tor-Faen | Pantygasseg WwTW | 3549 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326584 | 203132 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TG | NP47TG | np4 7tg | np47tg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3546 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326548 | 203145 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TH | NP47TH | np4 7th | np47th | Torfaen | Tor-Faen | Pantygasseg WwTW | 3419 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326594 | 202983 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TJ | NP47TJ | np4 7tj | np47tj | Torfaen | Tor-Faen | Pantygasseg WwTW | 3480 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 326478 | 203103 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TL | NP47TL | np4 7tl | np47tl | Torfaen | Tor-Faen | Pantygasseg WwTW | 3193 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 326184 | 202910 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TN | NP47TN | np4 7tn | np47tn | Torfaen | Tor-Faen | Pantygasseg WwTW | 3611 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326607 | 203189 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TP | NP47TP | np4 7tp | np47tp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3667 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326755 | 203181 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TQ | NP47TQ | np4 7tq | np47tq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3380 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 326269 | 203078 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TR | NP47TR | np4 7tr | np47tr | Torfaen | Tor-Faen | Pantygasseg WwTW | 3532 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 326447 | 203172 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TS | NP47TS | np4 7ts | np47ts | Torfaen | Tor-Faen | Pantygasseg WwTW | 3653 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326701 | 203192 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TT | NP47TT | np4 7tt | np47tt | Torfaen | Tor-Faen | Pantygasseg WwTW | 3616 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 326496 | 203243 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TU | NP47TU | np4 7tu | np47tu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3605 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 326417 | 203263 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TW | NP47TW | np4 7tw | np47tw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3630 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326717 | 203158 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TX | NP47TX | np4 7tx | np47tx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3455 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 325864 | 203275 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TY | NP47TY | np4 7ty | np47ty | Torfaen | Tor-Faen | Pantygasseg WwTW | 3321 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326626 | 202858 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7TZ | NP47TZ | np4 7tz | np47tz | Torfaen | Tor-Faen | Pantygasseg WwTW | 5654 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 326111 | 205468 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7UA | NP47UA | np4 7ua | np47ua | Torfaen | Tor-Faen | Pantygasseg WwTW | 5735 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 325892 | 205584 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7UD | NP47UD | np4 7ud | np47ud | Torfaen | Tor-Faen | Pantygasseg WwTW | 5478 | 1548 | Over1500 | 3.1 | 2.27 | 1.66 | 28.85 | 15.39 | 17.01 | 325499 | 205367 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7UE | NP47UE | np4 7ue | np47ue | Torfaen | Tor-Faen | Pantygasseg WwTW | 5284 | 1548 | Over1500 | 3.1 | 2.27 | 1.66 | 28.85 | 15.39 | 17.01 | 325430 | 205177 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7UF | NP47UF | np4 7uf | np47uf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4488 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325674 | 204356 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7UG | NP47UG | np4 7ug | np47ug | Torfaen | Tor-Faen | Pantygasseg WwTW | 4546 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325708 | 204410 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7UJ | NP47UJ | np4 7uj | np47uj | Torfaen | Tor-Faen | Pantygasseg WwTW | 6350 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 326380 | 206124 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7UL | NP47UL | np4 7ul | np47ul | Torfaen | Tor-Faen | Llanellen STW | 6337 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 326373 | 206179 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7UN | NP47UN | np4 7un | np47un | Torfaen | Tor-Faen | Llanellen STW | 6287 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 326485 | 206156 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7UQ | NP47UQ | np4 7uq | np47uq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4623 | 1548 | Over1500 | 3.1 | 2.27 | 1.66 | 28.85 | 15.39 | 17.01 | 325414 | 204516 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7UR | NP47UR | np4 7ur | np47ur | Torfaen | Tor-Faen | Pantygasseg WwTW | 3705 | 1595 | Over1500 | 3.19 | 2.34 | 1.71 | 29.73 | 15.86 | 17.52 | 325482 | 203590 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7US | NP47US | np4 7us | np47us | Torfaen | Tor-Faen | Pantygasseg WwTW | 3580 | 1586 | Over1500 | 3.17 | 2.32 | 1.7 | 29.56 | 15.77 | 17.43 | 325426 | 203470 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7UU | NP47UU | np4 7uu | np47uu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3643 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326798 | 203131 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 7UZ | NP47UZ | np4 7uz | np47uz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3561 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326778 | 203049 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AA | NP48AA | np4 8aa | np48aa | Torfaen | Tor-Faen | Little Mill STW | 4259 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 329796 | 200821 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AB | NP48AB | np4 8ab | np48ab | Torfaen | Tor-Faen | Pantygasseg WwTW | 4494 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 329558 | 200529 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AD | NP48AD | np4 8ad | np48ad | Torfaen | Tor-Faen | Little Mill STW | 4193 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 329871 | 200811 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AE | NP48AE | np4 8ae | np48ae | Torfaen | Tor-Faen | Little Mill STW | 4267 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 329768 | 200872 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AF | NP48AF | np4 8af | np48af | Torfaen | Tor-Faen | Little Mill STW | 4437 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 329631 | 200754 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AG | NP48AG | np4 8ag | np48ag | Torfaen | Tor-Faen | Pantygasseg WwTW | 4311 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329379 | 200490 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AH | NP48AH | np4 8ah | np48ah | Torfaen | Tor-Faen | Little Mill STW | 4516 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 329614 | 200590 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AJ | NP48AJ | np4 8aj | np48aj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4284 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329357 | 200445 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AL | NP48AL | np4 8al | np48al | Torfaen | Tor-Faen | Pantygasseg WwTW | 4459 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 329518 | 200561 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AN | NP48AN | np4 8an | np48an | Torfaen | Tor-Faen | Pantygasseg WwTW | 3914 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328986 | 200433 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AP | NP48AP | np4 8ap | np48ap | Torfaen | Tor-Faen | Pantygasseg WwTW | 3561 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328619 | 200498 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AQ | NP48AQ | np4 8aq | np48aq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4078 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 329141 | 200507 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AR | NP48AR | np4 8ar | np48ar | Torfaen | Tor-Faen | Pantygasseg WwTW | 3763 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 328825 | 200491 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AS | NP48AS | np4 8as | np48as | Torfaen | Tor-Faen | Little Mill STW | 4452 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 329649 | 200670 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AT | NP48AT | np4 8at | np48at | Torfaen | Tor-Faen | Pantygasseg WwTW | 3398 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328427 | 200634 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AU | NP48AU | np4 8au | np48au | Torfaen | Tor-Faen | Pantygasseg WwTW | 3318 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328348 | 200620 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AX | NP48AX | np4 8ax | np48ax | Torfaen | Tor-Faen | Pantygasseg WwTW | 3626 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328382 | 201463 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AY | NP48AY | np4 8ay | np48ay | Torfaen | Tor-Faen | Pantygasseg WwTW | 3597 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328650 | 200532 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8AZ | NP48AZ | np4 8az | np48az | Torfaen | Tor-Faen | Pantygasseg WwTW | 3297 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328351 | 200498 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BA | NP48BA | np4 8ba | np48ba | Torfaen | Tor-Faen | Pantygasseg WwTW | 3580 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328464 | 201151 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BB | NP48BB | np4 8bb | np48bb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3699 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328555 | 201246 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BD | NP48BD | np4 8bd | np48bd | Torfaen | Tor-Faen | Pantygasseg WwTW | 3488 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328298 | 201316 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BG | NP48BG | np4 8bg | np48bg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3626 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328408 | 201406 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BH | NP48BH | np4 8bh | np48bh | Torfaen | Tor-Faen | Pantygasseg WwTW | 3386 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328204 | 201275 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BJ | NP48BJ | np4 8bj | np48bj | Torfaen | Tor-Faen | Pantygasseg WwTW | 3686 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328560 | 201196 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BL | NP48BL | np4 8bl | np48bl | Torfaen | Tor-Faen | Pantygasseg WwTW | 3668 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328559 | 201147 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BN | NP48BN | np4 8bn | np48bn | Torfaen | Tor-Faen | Pantygasseg WwTW | 3731 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328564 | 201311 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BP | NP48BP | np4 8bp | np48bp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3893 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328671 | 201473 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BQ | NP48BQ | np4 8bq | np48bq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3575 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328405 | 201286 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BR | NP48BR | np4 8br | np48br | Torfaen | Tor-Faen | Pantygasseg WwTW | 3939 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328794 | 201294 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BS | NP48BS | np4 8bs | np48bs | Torfaen | Tor-Faen | Pantygasseg WwTW | 4040 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328824 | 201489 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BT | NP48BT | np4 8bt | np48bt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4022 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328818 | 201456 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BU | NP48BU | np4 8bu | np48bu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3947 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328777 | 201360 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BW | NP48BW | np4 8bw | np48bw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3865 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328686 | 201366 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BX | NP48BX | np4 8bx | np48bx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3745 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328547 | 201388 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BY | NP48BY | np4 8by | np48by | Torfaen | Tor-Faen | Pantygasseg WwTW | 3845 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328627 | 201453 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8BZ | NP48BZ | np4 8bz | np48bz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3753 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328522 | 201462 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DA | NP48DA | np4 8da | np48da | Torfaen | Tor-Faen | Pantygasseg WwTW | 3720 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328538 | 201345 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DB | NP48DB | np4 8db | np48db | Torfaen | Tor-Faen | Pantygasseg WwTW | 3501 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328353 | 201218 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DD | NP48DD | np4 8dd | np48dd | Torfaen | Tor-Faen | Pantygasseg WwTW | 3408 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328190 | 201360 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DE | NP48DE | np4 8de | np48de | Torfaen | Tor-Faen | Pantygasseg WwTW | 3345 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328194 | 201194 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DF | NP48DF | np4 8df | np48df | Torfaen | Tor-Faen | Pantygasseg WwTW | 3450 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328327 | 201145 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DG | NP48DG | np4 8dg | np48dg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3981 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328213 | 202396 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DH | NP48DH | np4 8dh | np48dh | Torfaen | Tor-Faen | Pantygasseg WwTW | 3825 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328258 | 202074 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DJ | NP48DJ | np4 8dj | np48dj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4047 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328457 | 202177 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DL | NP48DL | np4 8dl | np48dl | Torfaen | Tor-Faen | Pantygasseg WwTW | 3917 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328233 | 202265 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DN | NP48DN | np4 8dn | np48dn | Torfaen | Tor-Faen | Pantygasseg WwTW | 3924 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328264 | 202236 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DP | NP48DP | np4 8dp | np48dp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3717 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327930 | 202323 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DQ | NP48DQ | np4 8dq | np48dq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4028 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328189 | 202498 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DR | NP48DR | np4 8dr | np48dr | Torfaen | Tor-Faen | Pantygasseg WwTW | 3720 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327865 | 202402 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DS | NP48DS | np4 8ds | np48ds | Torfaen | Tor-Faen | Pantygasseg WwTW | 3833 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327961 | 202464 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DT | NP48DT | np4 8dt | np48dt | Torfaen | Tor-Faen | Pantygasseg WwTW | 3901 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 327910 | 202618 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DU | NP48DU | np4 8du | np48du | Torfaen | Tor-Faen | Pantygasseg WwTW | 3843 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 327902 | 202543 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DW | NP48DW | np4 8dw | np48dw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3955 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328256 | 202298 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DX | NP48DX | np4 8dx | np48dx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3853 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 327949 | 202507 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DY | NP48DY | np4 8dy | np48dy | Torfaen | Tor-Faen | Pantygasseg WwTW | 3809 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328153 | 202192 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8DZ | NP48DZ | np4 8dz | np48dz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3767 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327990 | 202330 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EA | NP48EA | np4 8ea | np48ea | Torfaen | Tor-Faen | Pantygasseg WwTW | 3846 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 327877 | 202574 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EB | NP48EB | np4 8eb | np48eb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3699 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327809 | 202431 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8ED | NP48ED | np4 8ed | np48ed | Torfaen | Tor-Faen | Pantygasseg WwTW | 3857 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 327853 | 202614 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EE | NP48EE | np4 8ee | np48ee | Torfaen | Tor-Faen | Pantygasseg WwTW | 3788 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327915 | 202448 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EF | NP48EF | np4 8ef | np48ef | Torfaen | Tor-Faen | Pantygasseg WwTW | 3763 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 327798 | 202535 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EG | NP48EG | np4 8eg | np48eg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3661 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328347 | 201610 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EH | NP48EH | np4 8eh | np48eh | Torfaen | Tor-Faen | Pantygasseg WwTW | 3796 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 327718 | 202660 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EJ | NP48EJ | np4 8ej | np48ej | Torfaen | Tor-Faen | Pantygasseg WwTW | 3719 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 327761 | 202511 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EL | NP48EL | np4 8el | np48el | Torfaen | Tor-Faen | Pantygasseg WwTW | 3665 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327709 | 202486 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EN | NP48EN | np4 8en | np48en | Torfaen | Tor-Faen | Pantygasseg WwTW | 3767 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327270 | 202989 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EP | NP48EP | np4 8ep | np48ep | Torfaen | Tor-Faen | Pantygasseg WwTW | 3742 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 327670 | 202631 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EQ | NP48EQ | np4 8eq | np48eq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4300 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329379 | 200400 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8ER | NP48ER | np4 8er | np48er | Torfaen | Tor-Faen | Pantygasseg WwTW | 4077 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329169 | 200260 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8ES | NP48ES | np4 8es | np48es | Torfaen | Tor-Faen | Pantygasseg WwTW | 4211 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329302 | 200282 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8ET | NP48ET | np4 8et | np48et | Torfaen | Tor-Faen | Pantygasseg WwTW | 4041 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329134 | 200243 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EU | NP48EU | np4 8eu | np48eu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3931 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329009 | 200387 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EW | NP48EW | np4 8ew | np48ew | Torfaen | Tor-Faen | Pantygasseg WwTW | 3391 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327275 | 202512 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EY | NP48EY | np4 8ey | np48ey | Torfaen | Tor-Faen | Pantygasseg WwTW | 3691 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327976 | 202228 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8EZ | NP48EZ | np4 8ez | np48ez | Torfaen | Tor-Faen | Pantygasseg WwTW | 3647 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327821 | 202342 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8FA | NP48FA | np4 8fa | np48fa | Torfaen | Tor-Faen | Pantygasseg WwTW | 4430 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329505 | 200442 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8FD | NP48FD | np4 8fd | np48fd | Torfaen | Tor-Faen | Pantygasseg WwTW | 3981 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 328110 | 202519 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8GA | NP48GA | np4 8ga | np48ga | Torfaen | Tor-Faen | Pantygasseg WwTW | 3556 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328274 | 201523 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HA | NP48HA | np4 8ha | np48ha | Torfaen | Tor-Faen | Pantygasseg WwTW | 3613 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327634 | 202488 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HB | NP48HB | np4 8hb | np48hb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3504 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327715 | 202246 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HD | NP48HD | np4 8hd | np48hd | Torfaen | Tor-Faen | Pantygasseg WwTW | 3491 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327588 | 202362 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HE | NP48HE | np4 8he | np48he | Torfaen | Tor-Faen | Pantygasseg WwTW | 3584 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327713 | 202366 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HF | NP48HF | np4 8hf | np48hf | Torfaen | Tor-Faen | Pantygasseg WwTW | 3595 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327844 | 202237 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HG | NP48HG | np4 8hg | np48hg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3648 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327984 | 202149 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HH | NP48HH | np4 8hh | np48hh | Torfaen | Tor-Faen | Pantygasseg WwTW | 3599 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 327512 | 202583 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HJ | NP48HJ | np4 8hj | np48hj | Torfaen | Tor-Faen | Pantygasseg WwTW | 3527 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327479 | 202515 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HL | NP48HL | np4 8hl | np48hl | Torfaen | Tor-Faen | Pantygasseg WwTW | 3463 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327468 | 202439 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HN | NP48HN | np4 8hn | np48hn | Torfaen | Tor-Faen | Pantygasseg WwTW | 3670 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328122 | 201998 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HP | NP48HP | np4 8hp | np48hp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3512 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327913 | 202018 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HQ | NP48HQ | np4 8hq | np48hq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3764 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328148 | 202123 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HR | NP48HR | np4 8hr | np48hr | Torfaen | Tor-Faen | Pantygasseg WwTW | 3335 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327827 | 201836 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HS | NP48HS | np4 8hs | np48hs | Torfaen | Tor-Faen | Pantygasseg WwTW | 3648 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328054 | 202055 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HT | NP48HT | np4 8ht | np48ht | Torfaen | Tor-Faen | Pantygasseg WwTW | 3539 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327876 | 202110 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HU | NP48HU | np4 8hu | np48hu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4000 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 329086 | 200322 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HW | NP48HW | np4 8hw | np48hw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4460 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329533 | 200456 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HY | NP48HY | np4 8hy | np48hy | Torfaen | Tor-Faen | Pantygasseg WwTW | 3345 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327601 | 202135 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8HZ | NP48HZ | np4 8hz | np48hz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3389 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327765 | 202008 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JA | NP48JA | np4 8ja | np48ja | Torfaen | Tor-Faen | Pantygasseg WwTW | 3899 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328391 | 202007 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JB | NP48JB | np4 8jb | np48jb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3958 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328390 | 202116 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JD | NP48JD | np4 8jd | np48jd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4136 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328465 | 202320 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JE | NP48JE | np4 8je | np48je | Torfaen | Tor-Faen | Pantygasseg WwTW | 3537 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327998 | 201944 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JF | NP48JF | np4 8jf | np48jf | Torfaen | Tor-Faen | Pantygasseg WwTW | 3767 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328240 | 201998 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JG | NP48JG | np4 8jg | np48jg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4212 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 328727 | 202058 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JH | NP48JH | np4 8jh | np48jh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4189 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 328581 | 202247 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JJ | NP48JJ | np4 8jj | np48jj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4258 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 328777 | 202064 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JL | NP48JL | np4 8jl | np48jl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4220 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 328664 | 202176 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JN | NP48JN | np4 8jn | np48jn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4054 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 328620 | 201929 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JP | NP48JP | np4 8jp | np48jp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4093 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 328571 | 202086 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JQ | NP48JQ | np4 8jq | np48jq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4286 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 328706 | 202232 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JR | NP48JR | np4 8jr | np48jr | Torfaen | Tor-Faen | Pantygasseg WwTW | 3981 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 328632 | 201756 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JS | NP48JS | np4 8js | np48js | Torfaen | Tor-Faen | Pantygasseg WwTW | 3758 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328465 | 201594 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JT | NP48JT | np4 8jt | np48jt | Torfaen | Tor-Faen | Pantygasseg WwTW | 3829 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 328584 | 201509 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JU | NP48JU | np4 8ju | np48ju | Torfaen | Tor-Faen | Pantygasseg WwTW | 3802 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328444 | 201728 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JW | NP48JW | np4 8jw | np48jw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4164 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 328641 | 202108 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JX | NP48JX | np4 8jx | np48jx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3796 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328478 | 201652 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JY | NP48JY | np4 8jy | np48jy | Torfaen | Tor-Faen | Pantygasseg WwTW | 3863 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328102 | 202345 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8JZ | NP48JZ | np4 8jz | np48jz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3803 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328061 | 202301 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LA | NP48LA | np4 8la | np48la | Torfaen | Tor-Faen | Pantygasseg WwTW | 3871 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328151 | 202297 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LB | NP48LB | np4 8lb | np48lb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3894 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 328157 | 202326 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LD | NP48LD | np4 8ld | np48ld | Torfaen | Tor-Faen | Pantygasseg WwTW | 3286 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327021 | 202576 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LE | NP48LE | np4 8le | np48le | Torfaen | Tor-Faen | Pantygasseg WwTW | 3199 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327595 | 201917 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LF | NP48LF | np4 8lf | np48lf | Torfaen | Tor-Faen | Pantygasseg WwTW | 3204 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 327506 | 202030 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LG | NP48LG | np4 8lg | np48lg | Torfaen | Tor-Faen | Pantygasseg WwTW | 3286 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327293 | 202359 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LH | NP48LH | np4 8lh | np48lh | Torfaen | Tor-Faen | Pantygasseg WwTW | 3241 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326982 | 202549 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LJ | NP48LJ | np4 8lj | np48lj | Torfaen | Tor-Faen | Pantygasseg WwTW | 3188 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327020 | 202455 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LL | NP48LL | np4 8ll | np48ll | Torfaen | Tor-Faen | Pantygasseg WwTW | 3180 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327032 | 202436 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LN | NP48LN | np4 8ln | np48ln | Torfaen | Tor-Faen | Pantygasseg WwTW | 3252 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327049 | 202513 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LP | NP48LP | np4 8lp | np48lp | Torfaen | Tor-Faen | Pantygasseg WwTW | 3229 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327136 | 202417 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LQ | NP48LQ | np4 8lq | np48lq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3311 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327151 | 202510 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LR | NP48LR | np4 8lr | np48lr | Torfaen | Tor-Faen | Pantygasseg WwTW | 3273 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327168 | 202448 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LS | NP48LS | np4 8ls | np48ls | Torfaen | Tor-Faen | Pantygasseg WwTW | 3197 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327144 | 202369 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LT | NP48LT | np4 8lt | np48lt | Torfaen | Tor-Faen | Pantygasseg WwTW | 3177 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327128 | 202357 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LU | NP48LU | np4 8lu | np48lu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3133 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327202 | 202235 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LW | NP48LW | np4 8lw | np48lw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3192 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327096 | 202402 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LX | NP48LX | np4 8lx | np48lx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3176 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327228 | 202269 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LY | NP48LY | np4 8ly | np48ly | Torfaen | Tor-Faen | Pantygasseg WwTW | 3120 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327185 | 202233 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8LZ | NP48LZ | np4 8lz | np48lz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3098 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327162 | 202224 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NA | NP48NA | np4 8na | np48na | Torfaen | Tor-Faen | Pantygasseg WwTW | 3193 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327250 | 202272 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NB | NP48NB | np4 8nb | np48nb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4308 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 328784 | 202150 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8ND | NP48ND | np4 8nd | np48nd | Torfaen | Tor-Faen | Pantygasseg WwTW | 3034 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327231 | 202072 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NE | NP48NE | np4 8ne | np48ne | Torfaen | Tor-Faen | Pantygasseg WwTW | 3062 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327231 | 202111 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NF | NP48NF | np4 8nf | np48nf | Torfaen | Tor-Faen | Pantygasseg WwTW | 3040 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327264 | 202048 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NG | NP48NG | np4 8ng | np48ng | Torfaen | Tor-Faen | Pantygasseg WwTW | 3147 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327269 | 202192 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NH | NP48NH | np4 8nh | np48nh | Torfaen | Tor-Faen | Pantygasseg WwTW | 3017 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327266 | 202013 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NJ | NP48NJ | np4 8nj | np48nj | Torfaen | Tor-Faen | Pantygasseg WwTW | 3027 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327297 | 201996 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NL | NP48NL | np4 8nl | np48nl | Torfaen | Tor-Faen | Pantygasseg WwTW | 3033 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327330 | 201969 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NN | NP48NN | np4 8nn | np48nn | Torfaen | Tor-Faen | Pantygasseg WwTW | 3123 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327295 | 202134 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NP | NP48NP | np4 8np | np48np | Torfaen | Tor-Faen | Pantygasseg WwTW | 3134 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327265 | 202178 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NQ | NP48NQ | np4 8nq | np48nq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3126 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327285 | 202148 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NR | NP48NR | np4 8nr | np48nr | Torfaen | Tor-Faen | Pantygasseg WwTW | 3127 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327336 | 202098 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NS | NP48NS | np4 8ns | np48ns | Torfaen | Tor-Faen | Pantygasseg WwTW | 3120 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327358 | 202066 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NT | NP48NT | np4 8nt | np48nt | Torfaen | Tor-Faen | Pantygasseg WwTW | 3106 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327365 | 202038 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NU | NP48NU | np4 8nu | np48nu | Torfaen | Tor-Faen | Pantygasseg WwTW | 3114 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327384 | 202030 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NW | NP48NW | np4 8nw | np48nw | Torfaen | Tor-Faen | Pantygasseg WwTW | 3119 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327315 | 202108 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NX | NP48NX | np4 8nx | np48nx | Torfaen | Tor-Faen | Pantygasseg WwTW | 3065 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327374 | 201969 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NY | NP48NY | np4 8ny | np48ny | Torfaen | Tor-Faen | Pantygasseg WwTW | 3096 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327435 | 201947 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8NZ | NP48NZ | np4 8nz | np48nz | Torfaen | Tor-Faen | Pantygasseg WwTW | 3096 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327435 | 201947 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PA | NP48PA | np4 8pa | np48pa | Torfaen | Tor-Faen | Pantygasseg WwTW | 3082 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327219 | 202150 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PB | NP48PB | np4 8pb | np48pb | Torfaen | Tor-Faen | Pantygasseg WwTW | 3078 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 327296 | 202070 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PD | NP48PD | np4 8pd | np48pd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4973 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 327004 | 204501 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PE | NP48PE | np4 8pe | np48pe | Torfaen | Tor-Faen | Pantygasseg WwTW | 4115 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326968 | 203575 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PF | NP48PF | np4 8pf | np48pf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4094 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326964 | 203553 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PH | NP48PH | np4 8ph | np48ph | Torfaen | Tor-Faen | Pantygasseg WwTW | 3936 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 326988 | 203362 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PJ | NP48PJ | np4 8pj | np48pj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4324 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 327023 | 203781 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PL | NP48PL | np4 8pl | np48pl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4564 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 327004 | 204055 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PN | NP48PN | np4 8pn | np48pn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4575 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326867 | 204127 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PP | NP48PP | np4 8pp | np48pp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4717 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326960 | 204242 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PQ | NP48PQ | np4 8pq | np48pq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4317 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326925 | 203820 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PR | NP48PR | np4 8pr | np48pr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4694 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326933 | 204228 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PS | NP48PS | np4 8ps | np48ps | Torfaen | Tor-Faen | Pantygasseg WwTW | 4947 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326952 | 204494 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PT | NP48PT | np4 8pt | np48pt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4660 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326904 | 204204 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PU | NP48PU | np4 8pu | np48pu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4928 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326998 | 204455 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PW | NP48PW | np4 8pw | np48pw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4464 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326936 | 203976 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PX | NP48PX | np4 8px | np48px | Torfaen | Tor-Faen | Pantygasseg WwTW | 4638 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326886 | 204187 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PY | NP48PY | np4 8py | np48py | Torfaen | Tor-Faen | Pantygasseg WwTW | 4529 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326628 | 204170 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8PZ | NP48PZ | np4 8pz | np48pz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4563 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326703 | 204179 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QA | NP48QA | np4 8qa | np48qa | Torfaen | Tor-Faen | Pantygasseg WwTW | 4511 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326829 | 204074 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QB | NP48QB | np4 8qb | np48qb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4515 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326798 | 204091 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QD | NP48QD | np4 8qd | np48qd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4069 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327030 | 203491 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QE | NP48QE | np4 8qe | np48qe | Torfaen | Tor-Faen | Pantygasseg WwTW | 4606 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326619 | 204255 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QF | NP48QF | np4 8qf | np48qf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4643 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326633 | 204289 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QG | NP48QG | np4 8qg | np48qg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4829 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326734 | 204451 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QH | NP48QH | np4 8qh | np48qh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4878 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326848 | 204461 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QJ | NP48QJ | np4 8qj | np48qj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4851 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326856 | 204429 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QL | NP48QL | np4 8ql | np48ql | Torfaen | Tor-Faen | Pantygasseg WwTW | 4496 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 327102 | 203934 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QP | NP48QP | np4 8qp | np48qp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4429 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 327155 | 203831 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QQ | NP48QQ | np4 8qq | np48qq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4647 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326767 | 204244 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QR | NP48QR | np4 8qr | np48qr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4478 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326863 | 204024 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QS | NP48QS | np4 8qs | np48qs | Torfaen | Tor-Faen | Pantygasseg WwTW | 4458 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326879 | 203995 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QT | NP48QT | np4 8qt | np48qt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4772 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326819 | 204358 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QU | NP48QU | np4 8qu | np48qu | Torfaen | Tor-Faen | Little Mill STW | 3948 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 329944 | 201357 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8QW | NP48QW | np4 8qw | np48qw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4378 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 327116 | 203794 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8QX | NP48QX | np4 8qx | np48qx | Torfaen | Tor-Faen | Little Mill STW | 3720 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 330066 | 201894 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8QY | NP48QY | np4 8qy | np48qy | Monmouthshire | Sir Fynwy | Little Mill STW | 3966 | 1378 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.68 | 13.7 | 15.14 | 329932 | 203468 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8QZ | NP48QZ | np4 8qz | np48qz | Monmouthshire | Sir Fynwy | Goytre STW | 3554 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 330926 | 204991 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8RB | NP48RB | np4 8rb | np48rb | Monmouthshire | Sir Fynwy | Little Mill STW | 3653 | 1378 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.68 | 13.7 | 15.14 | 330223 | 203348 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8RD | NP48RD | np4 8rd | np48rd | Monmouthshire | Sir Fynwy | Little Mill STW | 3971 | 1378 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.68 | 13.7 | 15.14 | 329812 | 202902 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8RE | NP48RE | np4 8re | np48re | Monmouthshire | Sir Fynwy | Little Mill STW | 3057 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 331240 | 204144 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8RF | NP48RF | np4 8rf | np48rf | Monmouthshire | Sir Fynwy | Little Mill STW | 3030 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 331279 | 204152 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8RG | NP48RG | np4 8rg | np48rg | Monmouthshire | Sir Fynwy | Goytre STW | 3737 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 330721 | 205518 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8RH | NP48RH | np4 8rh | np48rh | Monmouthshire | Sir Fynwy | Little Mill STW | 4016 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 330317 | 204481 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8RJ | NP48RJ | np4 8rj | np48rj | Monmouthshire | Sir Fynwy | Little Mill STW | 3097 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 331053 | 203921 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8RL | NP48RL | np4 8rl | np48rl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4447 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326940 | 203956 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8RN | NP48RN | np4 8rn | np48rn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4400 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 326743 | 203989 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8RP | NP48RP | np4 8rp | np48rp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4516 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329612 | 200227 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8RQ | NP48RQ | np4 8rq | np48rq | Monmouthshire | Sir Fynwy | Little Mill STW | 3483 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 331037 | 204583 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8RR | NP48RR | np4 8rr | np48rr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4472 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 329570 | 200197 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8SD | NP48SD | np4 8sd | np48sd | Monmouthshire | Sir Fynwy | Goytre STW | 3125 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 331341 | 205659 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8SJ | NP48SJ | np4 8sj | np48sj | Monmouthshire | Sir Fynwy | Goytre STW | 3036 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 331421 | 205332 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8SN | NP48SN | np4 8sn | np48sn | Monmouthshire | Sir Fynwy | Goytre STW | 3284 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 331179 | 205616 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8TP | NP48TP | np4 8tp | np48tp | Monmouthshire | Sir Fynwy | Little Mill STW | 4328 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 329482 | 203112 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8TR | NP48TR | np4 8tr | np48tr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4734 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 328148 | 203533 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8TS | NP48TS | np4 8ts | np48ts | Monmouthshire | Sir Fynwy | Little Mill STW | 4547 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 329236 | 202931 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8TT | NP48TT | np4 8tt | np48tt | Monmouthshire | Sir Fynwy | Little Mill STW | 4714 | 1462 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.25 | 14.53 | 16.06 | 329595 | 204623 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 8TU | NP48TU | np4 8tu | np48tu | Torfaen | Tor-Faen | Little Mill STW | 4468 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 329341 | 201685 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8UG | NP48UG | np4 8ug | np48ug | Torfaen | Tor-Faen | Llanellen STW | 6305 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 326542 | 206090 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8UH | NP48UH | np4 8uh | np48uh | Torfaen | Tor-Faen | Llanellen STW | 6251 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 326590 | 206121 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8UR | NP48UR | np4 8ur | np48ur | Torfaen | Tor-Faen | Llanellen STW | 5912 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 326818 | 206375 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8UU | NP48UU | np4 8uu | np48uu | Torfaen | Tor-Faen | Llanellen STW | 5653 | 1562 | Over1500 | 3.13 | 2.29 | 1.68 | 29.11 | 15.53 | 17.16 | 327045 | 206530 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8UW | NP48UW | np4 8uw | np48uw | Torfaen | Tor-Faen | Llanover STW | 5834 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 327087 | 206141 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8UY | NP48UY | np4 8uy | np48uy | Torfaen | Tor-Faen | Pantygasseg WwTW | 6124 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 326957 | 205741 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8UZ | NP48UZ | np4 8uz | np48uz | Torfaen | Tor-Faen | Llanover STW | 6037 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 326993 | 205918 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8XD | NP48XD | np4 8xd | np48xd | Torfaen | Tor-Faen | Llanover STW | 6053 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 326996 | 205886 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8XE | NP48XE | np4 8xe | np48xe | Torfaen | Tor-Faen | Llanover STW | 6017 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 326934 | 206041 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8XF | NP48XF | np4 8xf | np48xf | Torfaen | Tor-Faen | Llanover STW | 5973 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 327000 | 206020 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8XG | NP48XG | np4 8xg | np48xg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4969 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 327118 | 204448 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8XH | NP48XH | np4 8xh | np48xh | Torfaen | Tor-Faen | Llanellen STW | 5648 | 1562 | Over1500 | 3.13 | 2.29 | 1.68 | 29.11 | 15.53 | 17.16 | 326988 | 206577 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8XJ | NP48XJ | np4 8xj | np48xj | Torfaen | Tor-Faen | Pantygasseg WwTW | 5612 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 327043 | 205171 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8XL | NP48XL | np4 8xl | np48xl | Torfaen | Tor-Faen | Llanover STW | 5950 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 326909 | 206203 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8XQ | NP48XQ | np4 8xq | np48xq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5028 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 327209 | 204472 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 8XR | NP48XR | np4 8xr | np48xr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4847 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 327109 | 204318 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AA | NP49AA | np4 9aa | np49aa | Torfaen | Tor-Faen | Brynmawr STW | 5597 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325154 | 208888 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AB | NP49AB | np4 9ab | np49ab | Torfaen | Tor-Faen | Llanellen STW | 5540 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325195 | 209002 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AD | NP49AD | np4 9ad | np49ad | Torfaen | Tor-Faen | Brynmawr STW | 5516 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325108 | 208960 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AE | NP49AE | np4 9ae | np49ae | Torfaen | Tor-Faen | Brynmawr STW | 5494 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325029 | 208898 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AF | NP49AF | np4 9af | np49af | Torfaen | Tor-Faen | Brynmawr STW | 5311 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324914 | 209047 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AG | NP49AG | np4 9ag | np49ag | Torfaen | Tor-Faen | Brynmawr STW | 5346 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325017 | 209120 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AJ | NP49AJ | np4 9aj | np49aj | Torfaen | Tor-Faen | Brynmawr STW | 5467 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325071 | 208993 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AL | NP49AL | np4 9al | np49al | Torfaen | Tor-Faen | Llanellen STW | 5588 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325254 | 208754 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AN | NP49AN | np4 9an | np49an | Torfaen | Tor-Faen | Llanellen STW | 5591 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325273 | 208706 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AP | NP49AP | np4 9ap | np49ap | Torfaen | Tor-Faen | Llanellen STW | 5613 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325266 | 208672 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AQ | NP49AQ | np4 9aq | np49aq | Torfaen | Tor-Faen | Brynmawr STW | 5421 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325074 | 209070 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AR | NP49AR | np4 9ar | np49ar | Torfaen | Tor-Faen | Llanellen STW | 5586 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325303 | 208657 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AS | NP49AS | np4 9as | np49as | Torfaen | Tor-Faen | Brynmawr STW | 5550 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325044 | 208830 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AT | NP49AT | np4 9at | np49at | Torfaen | Tor-Faen | Llanellen STW | 5538 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325436 | 208507 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AU | NP49AU | np4 9au | np49au | Torfaen | Tor-Faen | Llanellen STW | 5630 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325325 | 208519 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AW | NP49AW | np4 9aw | np49aw | Torfaen | Tor-Faen | Llanellen STW | 5138 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325715 | 208835 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AX | NP49AX | np4 9ax | np49ax | Torfaen | Tor-Faen | Brynmawr STW | 3948 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 323430 | 209462 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AY | NP49AY | np4 9ay | np49ay | Torfaen | Tor-Faen | Llanellen STW | 5336 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 325868 | 208181 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9AZ | NP49AZ | np4 9az | np49az | Torfaen | Tor-Faen | Brynmawr STW | 4709 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 324473 | 209459 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BA | NP49BA | np4 9ba | np49ba | Torfaen | Tor-Faen | Llanellen STW | 5715 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325202 | 208572 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BB | NP49BB | np4 9bb | np49bb | Torfaen | Tor-Faen | Llanellen STW | 5480 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325376 | 208748 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BD | NP49BD | np4 9bd | np49bd | Torfaen | Tor-Faen | Llanellen STW | 5676 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325174 | 208716 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BE | NP49BE | np4 9be | np49be | Torfaen | Tor-Faen | Llanellen STW | 5746 | 1584 | Over1500 | 3.17 | 2.32 | 1.7 | 29.52 | 15.75 | 17.4 | 325304 | 208316 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BG | NP49BG | np4 9bg | np49bg | Torfaen | Tor-Faen | Llanellen STW | 5596 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325357 | 208531 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BH | NP49BH | np4 9bh | np49bh | Torfaen | Tor-Faen | Llanellen STW | 5661 | 1584 | Over1500 | 3.17 | 2.32 | 1.7 | 29.52 | 15.75 | 17.4 | 325301 | 208498 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BJ | NP49BJ | np4 9bj | np49bj | Torfaen | Tor-Faen | Brynmawr STW | 5714 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325101 | 208644 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BL | NP49BL | np4 9bl | np49bl | Torfaen | Tor-Faen | Brynmawr STW | 5587 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324992 | 208712 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BN | NP49BN | np4 9bn | np49bn | Torfaen | Tor-Faen | Brynmawr STW | 5368 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324800 | 208826 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BP | NP49BP | np4 9bp | np49bp | Torfaen | Tor-Faen | Brynmawr STW | 5373 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324774 | 208790 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BQ | NP49BQ | np4 9bq | np49bq | Torfaen | Tor-Faen | Llanellen STW | 5557 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325379 | 208572 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BR | NP49BR | np4 9br | np49br | Torfaen | Tor-Faen | Brynmawr STW | 5509 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324869 | 208693 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BS | NP49BS | np4 9bs | np49bs | Torfaen | Tor-Faen | Brynmawr STW | 5708 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324997 | 208538 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BT | NP49BT | np4 9bt | np49bt | Torfaen | Tor-Faen | Brynmawr STW | 5747 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325048 | 208535 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BU | NP49BU | np4 9bu | np49bu | Torfaen | Tor-Faen | Brynmawr STW | 5534 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324846 | 208630 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BW | NP49BW | np4 9bw | np49bw | Torfaen | Tor-Faen | Brynmawr STW | 5419 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324746 | 208692 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BX | NP49BX | np4 9bx | np49bx | Torfaen | Tor-Faen | Brynmawr STW | 5578 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324845 | 208566 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BY | NP49BY | np4 9by | np49by | Torfaen | Tor-Faen | Brynmawr STW | 5429 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324725 | 208656 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9BZ | NP49BZ | np4 9bz | np49bz | Torfaen | Tor-Faen | Brynmawr STW | 5462 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324951 | 208856 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DA | NP49DA | np4 9da | np49da | Torfaen | Tor-Faen | Brynmawr STW | 5452 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324604 | 208501 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DD | NP49DD | np4 9dd | np49dd | Torfaen | Tor-Faen | Brynmawr STW | 5452 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324604 | 208501 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DE | NP49DE | np4 9de | np49de | Torfaen | Tor-Faen | Brynmawr STW | 5413 | 1584 | Over1500 | 3.17 | 2.32 | 1.7 | 29.52 | 15.75 | 17.4 | 324523 | 208477 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DF | NP49DF | np4 9df | np49df | Torfaen | Tor-Faen | Brynmawr STW | 5381 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 324498 | 208498 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DG | NP49DG | np4 9dg | np49dg | Torfaen | Tor-Faen | Brynmawr STW | 5223 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 324327 | 208554 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DH | NP49DH | np4 9dh | np49dh | Torfaen | Tor-Faen | Brynmawr STW | 5338 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 324412 | 208477 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DJ | NP49DJ | np4 9dj | np49dj | Torfaen | Tor-Faen | Brynmawr STW | 5181 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 324332 | 208616 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DL | NP49DL | np4 9dl | np49dl | Torfaen | Tor-Faen | Brynmawr STW | 5211 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 324362 | 208603 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DN | NP49DN | np4 9dn | np49dn | Torfaen | Tor-Faen | Brynmawr STW | 5268 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 324445 | 208603 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DP | NP49DP | np4 9dp | np49dp | Torfaen | Tor-Faen | Brynmawr STW | 5309 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 324439 | 208541 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DQ | NP49DQ | np4 9dq | np49dq | Torfaen | Tor-Faen | Brynmawr STW | 5228 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 324316 | 208538 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DR | NP49DR | np4 9dr | np49dr | Torfaen | Tor-Faen | Llanellen STW | 5776 | 1584 | Over1500 | 3.17 | 2.32 | 1.7 | 29.52 | 15.75 | 17.4 | 325229 | 208388 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DS | NP49DS | np4 9ds | np49ds | Torfaen | Tor-Faen | Llanellen STW | 5721 | 1584 | Over1500 | 3.17 | 2.32 | 1.7 | 29.52 | 15.75 | 17.4 | 325274 | 208420 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DT | NP49DT | np4 9dt | np49dt | Torfaen | Tor-Faen | Brynmawr STW | 5102 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 324295 | 208689 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DX | NP49DX | np4 9dx | np49dx | Torfaen | Tor-Faen | Llanellen STW | 5531 | 1573 | Over1500 | 3.15 | 2.3 | 1.69 | 29.32 | 15.64 | 17.28 | 326488 | 207145 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DY | NP49DY | np4 9dy | np49dy | Torfaen | Tor-Faen | Llanellen STW | 5600 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 325591 | 208123 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9DZ | NP49DZ | np4 9dz | np49dz | Torfaen | Tor-Faen | Llanellen STW | 5385 | 1562 | Over1500 | 3.13 | 2.29 | 1.68 | 29.11 | 15.53 | 17.16 | 326743 | 207109 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EA | NP49EA | np4 9ea | np49ea | Torfaen | Tor-Faen | Llanellen STW | 5520 | 1562 | Over1500 | 3.13 | 2.29 | 1.68 | 29.11 | 15.53 | 17.16 | 326788 | 206894 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EB | NP49EB | np4 9eb | np49eb | Torfaen | Tor-Faen | Llanellen STW | 5613 | 1584 | Over1500 | 3.17 | 2.32 | 1.7 | 29.52 | 15.75 | 17.4 | 325435 | 208354 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9ED | NP49ED | np4 9ed | np49ed | Torfaen | Tor-Faen | Llanellen STW | 5113 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 326393 | 207855 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EE | NP49EE | np4 9ee | np49ee | Torfaen | Tor-Faen | Llanellen STW | 5705 | 1584 | Over1500 | 3.17 | 2.32 | 1.7 | 29.52 | 15.75 | 17.4 | 325368 | 208286 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EH | NP49EH | np4 9eh | np49eh | Torfaen | Tor-Faen | Llanellen STW | 5573 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325286 | 208722 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EJ | NP49EJ | np4 9ej | np49ej | Torfaen | Tor-Faen | Llanellen STW | 5566 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325274 | 208763 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EL | NP49EL | np4 9el | np49el | Torfaen | Tor-Faen | Llanellen STW | 5457 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325418 | 208715 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EN | NP49EN | np4 9en | np49en | Torfaen | Tor-Faen | Llanellen STW | 5467 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325386 | 208759 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EP | NP49EP | np4 9ep | np49ep | Torfaen | Tor-Faen | Llanellen STW | 5345 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325457 | 208892 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9ER | NP49ER | np4 9er | np49er | Torfaen | Tor-Faen | Llanellen STW | 5419 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325443 | 208752 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9ET | NP49ET | np4 9et | np49et | Torfaen | Tor-Faen | Llanellen STW | 5500 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325335 | 208788 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EU | NP49EU | np4 9eu | np49eu | Torfaen | Tor-Faen | Llanellen STW | 5443 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325375 | 208837 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EW | NP49EW | np4 9ew | np49ew | Torfaen | Tor-Faen | Llanellen STW | 5413 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325420 | 208813 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EX | NP49EX | np4 9ex | np49ex | Torfaen | Tor-Faen | Llanellen STW | 5450 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325371 | 208830 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EY | NP49EY | np4 9ey | np49ey | Torfaen | Tor-Faen | Llanellen STW | 5452 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325343 | 208885 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9EZ | NP49EZ | np4 9ez | np49ez | Torfaen | Tor-Faen | Llanellen STW | 5442 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325361 | 208870 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HA | NP49HA | np4 9ha | np49ha | Torfaen | Tor-Faen | Llanellen STW | 5477 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325314 | 208889 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HB | NP49HB | np4 9hb | np49hb | Torfaen | Tor-Faen | Llanellen STW | 5424 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325372 | 208888 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HD | NP49HD | np4 9hd | np49hd | Torfaen | Tor-Faen | Llanellen STW | 5374 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325403 | 208942 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HF | NP49HF | np4 9hf | np49hf | Torfaen | Tor-Faen | Llanellen STW | 5250 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325549 | 208920 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HG | NP49HG | np4 9hg | np49hg | Torfaen | Tor-Faen | Llanellen STW | 5245 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325569 | 208889 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HH | NP49HH | np4 9hh | np49hh | Torfaen | Tor-Faen | Llanellen STW | 5184 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325695 | 208772 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HJ | NP49HJ | np4 9hj | np49hj | Torfaen | Tor-Faen | Llanellen STW | 5161 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325766 | 208688 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HN | NP49HN | np4 9hn | np49hn | Torfaen | Tor-Faen | Llanellen STW | 5078 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325891 | 208634 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HP | NP49HP | np4 9hp | np49hp | Torfaen | Tor-Faen | Llanellen STW | 4911 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 326101 | 208606 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HQ | NP49HQ | np4 9hq | np49hq | Torfaen | Tor-Faen | Llanellen STW | 5223 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325586 | 208905 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HR | NP49HR | np4 9hr | np49hr | Torfaen | Tor-Faen | Llanellen STW | 5209 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325639 | 208828 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HS | NP49HS | np4 9hs | np49hs | Torfaen | Tor-Faen | Llanellen STW | 5007 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325959 | 208659 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HT | NP49HT | np4 9ht | np49ht | Torfaen | Tor-Faen | Llanellen STW | 4980 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 326057 | 208546 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HU | NP49HU | np4 9hu | np49hu | Torfaen | Tor-Faen | Llanellen STW | 4886 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 326235 | 208442 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HW | NP49HW | np4 9hw | np49hw | Torfaen | Tor-Faen | Llanellen STW | 5048 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325951 | 208590 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HX | NP49HX | np4 9hx | np49hx | Torfaen | Tor-Faen | Llanellen STW | 4857 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 326310 | 208383 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HY | NP49HY | np4 9hy | np49hy | Torfaen | Tor-Faen | Llanellen STW | 4767 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 326289 | 208577 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9HZ | NP49HZ | np4 9hz | np49hz | Torfaen | Tor-Faen | Llanellen STW | 4798 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 326073 | 208884 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JA | NP49JA | np4 9ja | np49ja | Torfaen | Tor-Faen | Llanellen STW | 4902 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325858 | 209080 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JB | NP49JB | np4 9jb | np49jb | Torfaen | Tor-Faen | Llanellen STW | 5101 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325675 | 209003 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JD | NP49JD | np4 9jd | np49jd | Torfaen | Tor-Faen | Llanellen STW | 4960 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325742 | 209197 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JE | NP49JE | np4 9je | np49je | Torfaen | Tor-Faen | Llanellen STW | 4898 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325796 | 209230 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JG | NP49JG | np4 9jg | np49jg | Torfaen | Tor-Faen | Llanellen STW | 4950 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325837 | 209012 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JH | NP49JH | np4 9jh | np49jh | Torfaen | Tor-Faen | Llanellen STW | 4950 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325866 | 208954 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JJ | NP49JJ | np4 9jj | np49jj | Torfaen | Tor-Faen | Llanellen STW | 4888 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325947 | 208930 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JL | NP49JL | np4 9jl | np49jl | Torfaen | Tor-Faen | Llanellen STW | 4855 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 326018 | 208866 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JN | NP49JN | np4 9jn | np49jn | Torfaen | Tor-Faen | Llanellen STW | 5521 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325371 | 208667 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JP | NP49JP | np4 9jp | np49jp | Torfaen | Tor-Faen | Llanellen STW | 5472 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325427 | 208664 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JQ | NP49JQ | np4 9jq | np49jq | Torfaen | Tor-Faen | Llanellen STW | 5109 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325865 | 208618 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JR | NP49JR | np4 9jr | np49jr | Torfaen | Tor-Faen | Llanellen STW | 4815 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 326133 | 208741 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JS | NP49JS | np4 9js | np49js | Torfaen | Tor-Faen | Llanellen STW | 5313 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325566 | 208743 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JT | NP49JT | np4 9jt | np49jt | Torfaen | Tor-Faen | Llanellen STW | 5322 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325527 | 208799 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JU | NP49JU | np4 9ju | np49ju | Torfaen | Tor-Faen | Llanellen STW | 5344 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325574 | 208659 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JW | NP49JW | np4 9jw | np49jw | Torfaen | Tor-Faen | Llanellen STW | 5574 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325324 | 208642 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JX | NP49JX | np4 9jx | np49jx | Torfaen | Tor-Faen | Llanellen STW | 5311 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325585 | 208709 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JY | NP49JY | np4 9jy | np49jy | Torfaen | Tor-Faen | Llanellen STW | 5267 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325639 | 208701 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9JZ | NP49JZ | np4 9jz | np49jz | Torfaen | Tor-Faen | Llanellen STW | 5290 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325638 | 208653 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LA | NP49LA | np4 9la | np49la | Torfaen | Tor-Faen | Llanellen STW | 5377 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325579 | 208581 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LB | NP49LB | np4 9lb | np49lb | Torfaen | Tor-Faen | Llanellen STW | 5415 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325514 | 208620 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LD | NP49LD | np4 9ld | np49ld | Torfaen | Tor-Faen | Llanellen STW | 5475 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325480 | 208557 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LE | NP49LE | np4 9le | np49le | Torfaen | Tor-Faen | Llanellen STW | 5395 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 325606 | 208494 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LF | NP49LF | np4 9lf | np49lf | Torfaen | Tor-Faen | Llanellen STW | 5324 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 325745 | 208398 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LG | NP49LG | np4 9lg | np49lg | Torfaen | Tor-Faen | Llanellen STW | 5246 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 325833 | 208402 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LH | NP49LH | np4 9lh | np49lh | Torfaen | Tor-Faen | Llanellen STW | 5334 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325648 | 208544 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LJ | NP49LJ | np4 9lj | np49lj | Torfaen | Tor-Faen | Llanellen STW | 5170 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325791 | 208625 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LL | NP49LL | np4 9ll | np49ll | Torfaen | Tor-Faen | Llanellen STW | 5210 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325768 | 208584 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LN | NP49LN | np4 9ln | np49ln | Torfaen | Tor-Faen | Llanellen STW | 5142 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325886 | 208515 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LP | NP49LP | np4 9lp | np49lp | Torfaen | Tor-Faen | Llanellen STW | 5211 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 325830 | 208475 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LQ | NP49LQ | np4 9lq | np49lq | Torfaen | Tor-Faen | Llanellen STW | 5317 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 325694 | 208497 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LR | NP49LR | np4 9lr | np49lr | Torfaen | Tor-Faen | Llanellen STW | 5239 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 325810 | 208454 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LS | NP49LS | np4 9ls | np49ls | Torfaen | Tor-Faen | Llanellen STW | 5269 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325673 | 208634 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LT | NP49LT | np4 9lt | np49lt | Torfaen | Tor-Faen | Llanellen STW | 4946 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 326047 | 208628 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LU | NP49LU | np4 9lu | np49lu | Torfaen | Tor-Faen | Llanellen STW | 4842 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 326199 | 208578 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LW | NP49LW | np4 9lw | np49lw | Torfaen | Tor-Faen | Llanellen STW | 5191 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325836 | 208504 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LX | NP49LX | np4 9lx | np49lx | Torfaen | Tor-Faen | Llanellen STW | 5140 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325846 | 208589 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LY | NP49LY | np4 9ly | np49ly | Torfaen | Tor-Faen | Llanellen STW | 5089 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325911 | 208578 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9LZ | NP49LZ | np4 9lz | np49lz | Torfaen | Tor-Faen | Llanellen STW | 5597 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325223 | 208799 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NA | NP49NA | np4 9na | np49na | Torfaen | Tor-Faen | Llanellen STW | 5633 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325200 | 208762 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NB | NP49NB | np4 9nb | np49nb | Torfaen | Tor-Faen | Llanellen STW | 5623 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325220 | 208744 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9ND | NP49ND | np4 9nd | np49nd | Torfaen | Tor-Faen | Llanellen STW | 5619 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325226 | 208741 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NE | NP49NE | np4 9ne | np49ne | Torfaen | Tor-Faen | Llanellen STW | 5524 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325276 | 208858 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NF | NP49NF | np4 9nf | np49nf | Torfaen | Tor-Faen | Llanellen STW | 5485 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325294 | 208912 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NG | NP49NG | np4 9ng | np49ng | Torfaen | Tor-Faen | Llanellen STW | 5329 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325424 | 209005 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NH | NP49NH | np4 9nh | np49nh | Torfaen | Tor-Faen | Llanellen STW | 5419 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325335 | 208983 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NJ | NP49NJ | np4 9nj | np49nj | Torfaen | Tor-Faen | Llanellen STW | 5389 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325361 | 208998 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NL | NP49NL | np4 9nl | np49nl | Torfaen | Tor-Faen | Llanellen STW | 5208 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325588 | 208936 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NN | NP49NN | np4 9nn | np49nn | Torfaen | Tor-Faen | Llanellen STW | 5195 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325577 | 208990 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NP | NP49NP | np4 9np | np49np | Torfaen | Tor-Faen | Llanellen STW | 5144 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325563 | 209150 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NQ | NP49NQ | np4 9nq | np49nq | Torfaen | Tor-Faen | Llanellen STW | 5234 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325512 | 209040 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NR | NP49NR | np4 9nr | np49nr | Torfaen | Tor-Faen | Llanellen STW | 5086 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325617 | 209170 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NS | NP49NS | np4 9ns | np49ns | Torfaen | Tor-Faen | Llanellen STW | 5102 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325578 | 209223 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NT | NP49NT | np4 9nt | np49nt | Torfaen | Tor-Faen | Llanellen STW | 5180 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325513 | 209176 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NU | NP49NU | np4 9nu | np49nu | Torfaen | Tor-Faen | Llanellen STW | 5188 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325492 | 209206 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NW | NP49NW | np4 9nw | np49nw | Torfaen | Tor-Faen | Llanellen STW | 5123 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325607 | 209100 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NX | NP49NX | np4 9nx | np49nx | Torfaen | Tor-Faen | Llanellen STW | 5105 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325538 | 209315 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NY | NP49NY | np4 9ny | np49ny | Torfaen | Tor-Faen | Llanellen STW | 5093 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325574 | 209256 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9NZ | NP49NZ | np4 9nz | np49nz | Torfaen | Tor-Faen | Llanellen STW | 5065 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325595 | 209280 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PA | NP49PA | np4 9pa | np49pa | Torfaen | Tor-Faen | Llanellen STW | 5081 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325555 | 209339 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PB | NP49PB | np4 9pb | np49pb | Torfaen | Tor-Faen | Llanellen STW | 5057 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325570 | 209366 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PD | NP49PD | np4 9pd | np49pd | Torfaen | Tor-Faen | Llanellen STW | 5032 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325621 | 209302 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PE | NP49PE | np4 9pe | np49pe | Torfaen | Tor-Faen | Llanellen STW | 4981 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325677 | 209301 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PF | NP49PF | np4 9pf | np49pf | Torfaen | Tor-Faen | Llanellen STW | 4998 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325630 | 209374 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PG | NP49PG | np4 9pg | np49pg | Torfaen | Tor-Faen | Llanellen STW | 4951 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325654 | 209443 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PH | NP49PH | np4 9ph | np49ph | Torfaen | Tor-Faen | Llanellen STW | 5028 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325598 | 209374 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PJ | NP49PJ | np4 9pj | np49pj | Torfaen | Tor-Faen | Llanellen STW | 4978 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325742 | 209153 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PL | NP49PL | np4 9pl | np49pl | Torfaen | Tor-Faen | Llanellen STW | 5051 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325699 | 209069 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PN | NP49PN | np4 9pn | np49pn | Torfaen | Tor-Faen | Llanellen STW | 5295 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325477 | 208968 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PP | NP49PP | np4 9pp | np49pp | Torfaen | Tor-Faen | Llanellen STW | 5084 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325682 | 209027 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PQ | NP49PQ | np4 9pq | np49pq | Torfaen | Tor-Faen | Llanellen STW | 4985 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 325620 | 209438 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PR | NP49PR | np4 9pr | np49pr | Torfaen | Tor-Faen | Llanellen STW | 4832 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 326227 | 208554 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PS | NP49PS | np4 9ps | np49ps | Torfaen | Tor-Faen | Llanellen STW | 5489 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325261 | 208978 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PT | NP49PT | np4 9pt | np49pt | Torfaen | Tor-Faen | Llanellen STW | 5604 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325195 | 208844 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PU | NP49PU | np4 9pu | np49pu | Torfaen | Tor-Faen | Llanellen STW | 5567 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325212 | 208896 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PY | NP49PY | np4 9py | np49py | Torfaen | Tor-Faen | Llanellen STW | 5523 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325255 | 208908 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9PZ | NP49PZ | np4 9pz | np49pz | Torfaen | Tor-Faen | Llanellen STW | 5525 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325221 | 208980 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QA | NP49QA | np4 9qa | np49qa | Torfaen | Tor-Faen | Llanellen STW | 5435 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325316 | 208987 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QB | NP49QB | np4 9qb | np49qb | Torfaen | Tor-Faen | Llanellen STW | 5456 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325282 | 209012 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QD | NP49QD | np4 9qd | np49qd | Torfaen | Tor-Faen | Llanellen STW | 5435 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325286 | 209057 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QE | NP49QE | np4 9qe | np49qe | Torfaen | Tor-Faen | Llanellen STW | 5507 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325201 | 209075 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QF | NP49QF | np4 9qf | np49qf | Torfaen | Tor-Faen | Llanellen STW | 5493 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325205 | 209101 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QG | NP49QG | np4 9qg | np49qg | Torfaen | Tor-Faen | Brynmawr STW | 5452 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325190 | 209172 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QH | NP49QH | np4 9qh | np49qh | Torfaen | Tor-Faen | Llanellen STW | 5348 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325362 | 209102 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QJ | NP49QJ | np4 9qj | np49qj | Torfaen | Tor-Faen | Llanellen STW | 5380 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325282 | 209216 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QL | NP49QL | np4 9ql | np49ql | Torfaen | Tor-Faen | Llanellen STW | 5439 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325227 | 209193 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QN | NP49QN | np4 9qn | np49qn | Torfaen | Tor-Faen | Llanellen STW | 5256 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325342 | 209411 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QP | NP49QP | np4 9qp | np49qp | Torfaen | Tor-Faen | Llanellen STW | 5308 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325353 | 209230 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QQ | NP49QQ | np4 9qq | np49qq | Torfaen | Tor-Faen | Llanellen STW | 5456 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325232 | 209133 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QR | NP49QR | np4 9qr | np49qr | Torfaen | Tor-Faen | Llanellen STW | 5305 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325288 | 209416 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QS | NP49QS | np4 9qs | np49qs | Torfaen | Tor-Faen | Llanellen STW | 5282 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325289 | 209484 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QT | NP49QT | np4 9qt | np49qt | Torfaen | Tor-Faen | Llanellen STW | 5137 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 325409 | 209584 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QU | NP49QU | np4 9qu | np49qu | Torfaen | Tor-Faen | Llanellen STW | 5125 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 325437 | 209539 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QW | NP49QW | np4 9qw | np49qw | Torfaen | Tor-Faen | Llanellen STW | 5285 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325304 | 209433 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QX | NP49QX | np4 9qx | np49qx | Torfaen | Tor-Faen | Llanellen STW | 5166 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325435 | 209417 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QY | NP49QY | np4 9qy | np49qy | Torfaen | Tor-Faen | Llanellen STW | 5248 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325390 | 209301 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9QZ | NP49QZ | np4 9qz | np49qz | Torfaen | Tor-Faen | Llanellen STW | 5150 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325497 | 209296 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9RA | NP49RA | np4 9ra | np49ra | Torfaen | Tor-Faen | Llanellen STW | 5304 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325372 | 209193 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9RB | NP49RB | np4 9rb | np49rb | Torfaen | Tor-Faen | Llanellen STW | 5366 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325319 | 209160 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9RE | NP49RE | np4 9re | np49re | Torfaen | Tor-Faen | Brynmawr STW | 5358 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324895 | 208951 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9RF | NP49RF | np4 9rf | np49rf | Torfaen | Tor-Faen | Brynmawr STW | 5282 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324883 | 209054 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9RG | NP49RG | np4 9rg | np49rg | Torfaen | Tor-Faen | Brynmawr STW | 5388 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325180 | 209268 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9RJ | NP49RJ | np4 9rj | np49rj | Torfaen | Tor-Faen | Brynmawr STW | 5108 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324685 | 209089 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9RL | NP49RL | np4 9rl | np49rl | Torfaen | Tor-Faen | Brynmawr STW | 4935 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324507 | 209148 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9RN | NP49RN | np4 9rn | np49rn | Torfaen | Tor-Faen | Brynmawr STW | 5288 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325030 | 209232 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9RQ | NP49RQ | np4 9rq | np49rq | Torfaen | Tor-Faen | Brynmawr STW | 5307 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325061 | 209242 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9RR | NP49RR | np4 9rr | np49rr | Torfaen | Tor-Faen | Brynmawr STW | 4891 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 324628 | 209361 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9RT | NP49RT | np4 9rt | np49rt | Torfaen | Tor-Faen | Brynmawr STW | 4298 | 1495 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.86 | 14.86 | 16.43 | 324084 | 209633 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9RX | NP49RX | np4 9rx | np49rx | Torfaen | Tor-Faen | Brynmawr STW | 4351 | 1495 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.86 | 14.86 | 16.43 | 324140 | 209616 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9SB | NP49SB | np4 9sb | np49sb | Torfaen | Tor-Faen | Brynmawr STW | 4429 | 1495 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.86 | 14.86 | 16.43 | 324199 | 209566 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9SD | NP49SD | np4 9sd | np49sd | Torfaen | Tor-Faen | Brynmawr STW | 4226 | 1495 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.86 | 14.86 | 16.43 | 324021 | 209669 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9SE | NP49SE | np4 9se | np49se | Torfaen | Tor-Faen | Brynmawr STW | 3567 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 323496 | 210070 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9SF | NP49SF | np4 9sf | np49sf | Torfaen | Tor-Faen | Brynmawr STW | 3709 | 1495 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.86 | 14.86 | 16.43 | 323539 | 209904 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9SG | NP49SG | np4 9sg | np49sg | Torfaen | Tor-Faen | Brynmawr STW | 3655 | 1495 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.86 | 14.86 | 16.43 | 323541 | 209988 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9SJ | NP49SJ | np4 9sj | np49sj | Torfaen | Tor-Faen | Brynmawr STW | 3329 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 322810 | 209753 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9SR | NP49SR | np4 9sr | np49sr | Torfaen | Tor-Faen | Aberbaiden STW | 5049 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 325192 | 209864 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9SS | NP49SS | np4 9ss | np49ss | Monmouthshire | Sir Fynwy | Aberbaiden STW | 3543 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 324637 | 211676 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP4 9XA | NP49XA | np4 9xa | np49xa | Torfaen | Tor-Faen | Llanellen STW | 5678 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 325168 | 208726 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9XG | NP49XG | np4 9xg | np49xg | Torfaen | Tor-Faen | Brynmawr STW | 4879 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 324133 | 208843 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP4 9XP | NP49XP | np4 9xp | np49xp | Torfaen | Tor-Faen | Brynmawr STW | 4734 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 323763 | 208715 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AA | NP441AA | np44 1aa | np441aa | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4979 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329113 | 196296 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AB | NP441AB | np44 1ab | np441ab | Torfaen | Tor-Faen | Pantygasseg WwTW | 4181 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328311 | 197219 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AD | NP441AD | np44 1ad | np441ad | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5155 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328943 | 196341 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AE | NP441AE | np44 1ae | np441ae | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5013 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329082 | 196313 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AF | NP441AF | np44 1af | np441af | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5047 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329054 | 196345 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AG | NP441AG | np44 1ag | np441ag | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5141 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328946 | 196280 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AH | NP441AH | np44 1ah | np441ah | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4638 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329366 | 195494 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AJ | NP441AJ | np44 1aj | np441aj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4638 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329366 | 195494 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AL | NP441AL | np44 1al | np441al | Torfaen | Tor-Faen | Pantygasseg WwTW | 5146 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328896 | 196423 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AN | NP441AN | np44 1an | np441an | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5143 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328952 | 196326 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AP | NP441AP | np44 1ap | np441ap | Torfaen | Tor-Faen | Pantygasseg WwTW | 4833 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328899 | 196908 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AQ | NP441AQ | np44 1aq | np441aq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5108 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328971 | 196235 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AR | NP441AR | np44 1ar | np441ar | Torfaen | Tor-Faen | Pantygasseg WwTW | 5078 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328829 | 196451 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AS | NP441AS | np44 1as | np441as | Torfaen | Tor-Faen | Pantygasseg WwTW | 5056 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328790 | 196442 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AT | NP441AT | np44 1at | np441at | Torfaen | Tor-Faen | Pantygasseg WwTW | 5094 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328695 | 196290 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AU | NP441AU | np44 1au | np441au | Torfaen | Tor-Faen | Pantygasseg WwTW | 4980 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328717 | 196475 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AW | NP441AW | np44 1aw | np441aw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4972 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328664 | 196432 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AX | NP441AX | np44 1ax | np441ax | Torfaen | Tor-Faen | Pantygasseg WwTW | 5002 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328695 | 196420 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AY | NP441AY | np44 1ay | np441ay | Torfaen | Tor-Faen | Pantygasseg WwTW | 4902 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328628 | 196494 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1AZ | NP441AZ | np44 1az | np441az | Torfaen | Tor-Faen | Pantygasseg WwTW | 4874 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328608 | 196514 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BA | NP441BA | np44 1ba | np441ba | Torfaen | Tor-Faen | Pantygasseg WwTW | 4919 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328659 | 196502 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BB | NP441BB | np44 1bb | np441bb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4859 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328601 | 196528 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BD | NP441BD | np44 1bd | np441bd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4835 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328589 | 196550 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BE | NP441BE | np44 1be | np441be | Torfaen | Tor-Faen | Pantygasseg WwTW | 4630 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328522 | 196779 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BG | NP441BG | np44 1bg | np441bg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4635 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328611 | 196871 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BH | NP441BH | np44 1bh | np441bh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4694 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328501 | 196663 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BJ | NP441BJ | np44 1bj | np441bj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4764 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328623 | 196690 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BL | NP441BL | np44 1bl | np441bl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4974 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329118 | 196963 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BN | NP441BN | np44 1bn | np441bn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4829 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328687 | 196665 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BP | NP441BP | np44 1bp | np441bp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4802 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328724 | 196747 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BQ | NP441BQ | np44 1bq | np441bq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4630 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328633 | 196905 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BS | NP441BS | np44 1bs | np441bs | Torfaen | Tor-Faen | Pantygasseg WwTW | 4960 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329058 | 196907 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BT | NP441BT | np44 1bt | np441bt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4729 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328695 | 196825 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BU | NP441BU | np44 1bu | np441bu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4693 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329016 | 197307 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BW | NP441BW | np44 1bw | np441bw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4738 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328573 | 196675 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BX | NP441BX | np44 1bx | np441bx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4716 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329267 | 197684 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BY | NP441BY | np44 1by | np441by | Torfaen | Tor-Faen | Pantygasseg WwTW | 4572 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328627 | 196987 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1BZ | NP441BZ | np44 1bz | np441bz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DA | NP441DA | np44 1da | np441da | Torfaen | Tor-Faen | Pantygasseg WwTW | 4215 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328503 | 197408 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DB | NP441DB | np44 1db | np441db | Torfaen | Tor-Faen | Pantygasseg WwTW | 4531 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328635 | 197062 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DD | NP441DD | np44 1dd | np441dd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4562 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328710 | 197107 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DE | NP441DE | np44 1de | np441de | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4729 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329732 | 197382 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DF | NP441DF | np44 1df | np441df | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4308 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329699 | 195561 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DG | NP441DG | np44 1dg | np441dg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4838 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329407 | 197688 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DH | NP441DH | np44 1dh | np441dh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4870 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329345 | 197505 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DJ | NP441DJ | np44 1dj | np441dj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4696 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329214 | 197627 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DL | NP441DL | np44 1dl | np441dl | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4937 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329114 | 196043 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DN | NP441DN | np44 1dn | np441dn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4935 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329137 | 196178 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DP | NP441DP | np44 1dp | np441dp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5016 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329024 | 195972 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DQ | NP441DQ | np44 1dq | np441dq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4983 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329120 | 196349 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DR | NP441DR | np44 1dr | np441dr | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5010 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329040 | 196045 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DS | NP441DS | np44 1ds | np441ds | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4992 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329066 | 196099 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DT | NP441DT | np44 1dt | np441dt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4898 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329169 | 196149 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DU | NP441DU | np44 1du | np441du | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4893 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329183 | 196200 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DW | NP441DW | np44 1dw | np441dw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4927 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329158 | 196253 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DX | NP441DX | np44 1dx | np441dx | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4859 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329258 | 196403 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DY | NP441DY | np44 1dy | np441dy | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4921 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329180 | 196332 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1DZ | NP441DZ | np44 1dz | np441dz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4899 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329196 | 196303 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EA | NP441EA | np44 1ea | np441ea | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4922 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329189 | 196381 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EB | NP441EB | np44 1eb | np441eb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4923 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329222 | 196529 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1ED | NP441ED | np44 1ed | np441ed | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5061 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329069 | 196484 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EE | NP441EE | np44 1ee | np441ee | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4917 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329190 | 196360 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EF | NP441EF | np44 1ef | np441ef | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4908 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329217 | 196442 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EG | NP441EG | np44 1eg | np441eg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4946 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329160 | 196359 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EH | NP441EH | np44 1eh | np441eh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5055 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329064 | 196433 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EJ | NP441EJ | np44 1ej | np441ej | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5047 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329060 | 196376 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EL | NP441EL | np44 1el | np441el | Torfaen | Tor-Faen | Pantygasseg WwTW | 4880 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328895 | 196829 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EN | NP441EN | np44 1en | np441en | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4875 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329258 | 196474 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EP | NP441EP | np44 1ep | np441ep | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5036 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329037 | 196192 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EQ | NP441EQ | np44 1eq | np441eq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4983 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329142 | 196450 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1ER | NP441ER | np44 1er | np441er | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5073 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329071 | 196544 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1ES | NP441ES | np44 1es | np441es | Torfaen | Tor-Faen | Pantygasseg WwTW | 4698 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328444 | 196598 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1ET | NP441ET | np44 1et | np441et | Torfaen | Tor-Faen | Pantygasseg WwTW | 4641 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328419 | 196654 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EU | NP441EU | np44 1eu | np441eu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4604 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328376 | 196663 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EW | NP441EW | np44 1ew | np441ew | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4845 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329296 | 196503 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EX | NP441EX | np44 1ex | np441ex | Torfaen | Tor-Faen | Pantygasseg WwTW | 4482 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328294 | 196754 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EY | NP441EY | np44 1ey | np441ey | Torfaen | Tor-Faen | Pantygasseg WwTW | 4776 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328518 | 196562 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1EZ | NP441EZ | np44 1ez | np441ez | Torfaen | Tor-Faen | Pantygasseg WwTW | 4604 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328330 | 196618 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FA | NP441FA | np44 1fa | np441fa | Torfaen | Tor-Faen | Pantygasseg WwTW | 4929 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329373 | 197435 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FB | NP441FB | np44 1fb | np441fb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4799 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329271 | 197520 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FD | NP441FD | np44 1fd | np441fd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4961 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 329543 | 197683 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FE | NP441FE | np44 1fe | np441fe | Torfaen | Tor-Faen | Pantygasseg WwTW | 4825 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329372 | 197649 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FF | NP441FF | np44 1ff | np441ff | Torfaen | Tor-Faen | Pantygasseg WwTW | 4840 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329437 | 197741 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FG | NP441FG | np44 1fg | np441fg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4655 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329261 | 197804 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FH | NP441FH | np44 1fh | np441fh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4746 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329095 | 197332 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FJ | NP441FJ | np44 1fj | np441fj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4929 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329271 | 197267 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FL | NP441FL | np44 1fl | np441fl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4763 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329064 | 197254 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FN | NP441FN | np44 1fn | np441fn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4897 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329167 | 197167 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FQ | NP441FQ | np44 1fq | np441fq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4746 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329226 | 197548 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FR | NP441FR | np44 1fr | np441fr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4387 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328948 | 197785 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FS | NP441FS | np44 1fs | np441fs | Torfaen | Tor-Faen | Pantygasseg WwTW | 4436 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328955 | 197697 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FT | NP441FT | np44 1ft | np441ft | Torfaen | Tor-Faen | Pantygasseg WwTW | 4508 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329048 | 197716 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FU | NP441FU | np44 1fu | np441fu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4419 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328910 | 197654 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FW | NP441FW | np44 1fw | np441fw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4537 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 329129 | 197805 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FY | NP441FY | np44 1fy | np441fy | Torfaen | Tor-Faen | Pantygasseg WwTW | 4404 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328779 | 197474 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1FZ | NP441FZ | np44 1fz | np441fz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4635 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328195 | 196449 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1GB | NP441GB | np44 1gb | np441gb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4334 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 328754 | 197563 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HA | NP441HA | np44 1ha | np441ha | Torfaen | Tor-Faen | Pantygasseg WwTW | 4516 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328287 | 196698 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HB | NP441HB | np44 1hb | np441hb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4555 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328303 | 196660 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HD | NP441HD | np44 1hd | np441hd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4432 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328140 | 196674 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HE | NP441HE | np44 1he | np441he | Torfaen | Tor-Faen | Pantygasseg WwTW | 4427 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328198 | 196736 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HF | NP441HF | np44 1hf | np441hf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4328 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328107 | 196785 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HG | NP441HG | np44 1hg | np441hg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4500 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328154 | 196594 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HH | NP441HH | np44 1hh | np441hh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4317 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328135 | 196828 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HJ | NP441HJ | np44 1hj | np441hj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4540 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328212 | 196593 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HL | NP441HL | np44 1hl | np441hl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4635 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328291 | 196537 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HN | NP441HN | np44 1hn | np441hn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4598 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328190 | 196494 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HP | NP441HP | np44 1hp | np441hp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4271 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328063 | 196822 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HQ | NP441HQ | np44 1hq | np441hq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4586 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328230 | 196547 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HR | NP441HR | np44 1hr | np441hr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4365 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328075 | 196705 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1HW | NP441HW | np44 1hw | np441hw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4495 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328117 | 196567 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1JL | NP441JL | np44 1jl | np441jl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4889 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328596 | 196481 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1JN | NP441JN | np44 1jn | np441jn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4844 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328524 | 196472 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1JP | NP441JP | np44 1jp | np441jp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4903 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328582 | 196446 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1JR | NP441JR | np44 1jr | np441jr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4992 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328457 | 196205 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1JS | NP441JS | np44 1js | np441js | Torfaen | Tor-Faen | Pantygasseg WwTW | 4757 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328319 | 196397 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1JT | NP441JT | np44 1jt | np441jt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4839 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328377 | 196338 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1JU | NP441JU | np44 1ju | np441ju | Torfaen | Tor-Faen | Pantygasseg WwTW | 4835 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328428 | 196392 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1JW | NP441JW | np44 1jw | np441jw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4909 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328485 | 196344 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1JX | NP441JX | np44 1jx | np441jx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4785 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328395 | 196429 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1JY | NP441JY | np44 1jy | np441jy | Torfaen | Tor-Faen | Pantygasseg WwTW | 4692 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328309 | 196476 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1JZ | NP441JZ | np44 1jz | np441jz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4806 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328446 | 196448 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LA | NP441LA | np44 1la | np441la | Torfaen | Tor-Faen | Pantygasseg WwTW | 4778 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328468 | 196509 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LB | NP441LB | np44 1lb | np441lb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5130 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328910 | 195974 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LD | NP441LD | np44 1ld | np441ld | Torfaen | Tor-Faen | Pantygasseg WwTW | 4852 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328371 | 196316 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LE | NP441LE | np44 1le | np441le | Torfaen | Tor-Faen | Pantygasseg WwTW | 4738 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328273 | 196380 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LF | NP441LF | np44 1lf | np441lf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4928 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328428 | 196265 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LG | NP441LG | np44 1lg | np441lg | Torfaen | Tor-Faen | Pantygasseg WwTW | 5180 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328676 | 196151 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LH | NP441LH | np44 1lh | np441lh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4802 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329303 | 196341 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LJ | NP441LJ | np44 1lj | np441lj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4774 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329340 | 196379 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LL | NP441LL | np44 1ll | np441ll | Torfaen | Tor-Faen | Pantygasseg WwTW | 5196 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328810 | 196261 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LN | NP441LN | np44 1ln | np441ln | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5221 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328823 | 196011 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LP | NP441LP | np44 1lp | np441lp | Torfaen | Tor-Faen | Pantygasseg WwTW | 5200 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328871 | 196317 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LQ | NP441LQ | np44 1lq | np441lq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5248 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328821 | 196197 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LR | NP441LR | np44 1lr | np441lr | Torfaen | Tor-Faen | Pantygasseg WwTW | 5273 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328733 | 196077 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LS | NP441LS | np44 1ls | np441ls | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5202 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328858 | 196124 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LT | NP441LT | np44 1lt | np441lt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5171 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328877 | 196042 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LU | NP441LU | np44 1lu | np441lu | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5128 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328919 | 196028 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LW | NP441LW | np44 1lw | np441lw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5146 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328920 | 196159 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LY | NP441LY | np44 1ly | np441ly | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4678 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329343 | 195772 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1LZ | NP441LZ | np44 1lz | np441lz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4686 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329346 | 195887 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NA | NP441NA | np44 1na | np441na | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4714 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329335 | 196016 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NB | NP441NB | np44 1nb | np441nb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4738 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329327 | 196120 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1ND | NP441ND | np44 1nd | np441nd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4676 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329374 | 196020 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NE | NP441NE | np44 1ne | np441ne | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4735 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329283 | 195738 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NF | NP441NF | np44 1nf | np441nf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4647 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329371 | 195739 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NG | NP441NG | np44 1ng | np441ng | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4742 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329280 | 195793 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NH | NP441NH | np44 1nh | np441nh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4776 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329273 | 196022 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NJ | NP441NJ | np44 1nj | np441nj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4789 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329273 | 196109 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NL | NP441NL | np44 1nl | np441nl | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4805 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329273 | 196204 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NN | NP441NN | np44 1nn | np441nn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4747 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329283 | 195870 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NP | NP441NP | np44 1np | np441np | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4707 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329367 | 196172 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NQ | NP441NQ | np44 1nq | np441nq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4653 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329373 | 195822 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NS | NP441NS | np44 1ns | np441ns | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4725 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329382 | 196340 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NT | NP441NT | np44 1nt | np441nt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4604 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329461 | 196112 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NU | NP441NU | np44 1nu | np441nu | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4560 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329507 | 196122 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NW | NP441NW | np44 1nw | np441nw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4757 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329280 | 195925 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NY | NP441NY | np44 1ny | np441ny | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4480 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329604 | 196205 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1NZ | NP441NZ | np44 1nz | np441nz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4692 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329396 | 196248 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PB | NP441PB | np44 1pb | np441pb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4615 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329387 | 195358 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PD | NP441PD | np44 1pd | np441pd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4441 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329564 | 195534 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PE | NP441PE | np44 1pe | np441pe | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4590 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329412 | 195301 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1PZ | NP441PZ | np44 1pz | np441pz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4626 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329402 | 195844 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QA | NP441QA | np44 1qa | np441qa | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4616 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329427 | 195968 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QB | NP441QB | np44 1qb | np441qb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4565 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329455 | 195765 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QD | NP441QD | np44 1qd | np441qd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4556 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329491 | 195994 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QE | NP441QE | np44 1qe | np441qe | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4637 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329402 | 195936 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QF | NP441QF | np44 1qf | np441qf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4487 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329547 | 195888 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QG | NP441QG | np44 1qg | np441qg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4510 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329510 | 195755 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QH | NP441QH | np44 1qh | np441qh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4501 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329553 | 196036 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QJ | NP441QJ | np44 1qj | np441qj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4555 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329486 | 195945 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QL | NP441QL | np44 1ql | np441ql | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4585 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329440 | 195813 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QN | NP441QN | np44 1qn | np441qn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4478 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329548 | 195819 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QP | NP441QP | np44 1qp | np441qp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4484 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329534 | 195736 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QQ | NP441QQ | np44 1qq | np441qq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4552 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329478 | 195859 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QR | NP441QR | np44 1qr | np441qr | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4616 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329387 | 195476 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QS | NP441QS | np44 1qs | np441qs | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4438 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329571 | 195613 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QT | NP441QT | np44 1qt | np441qt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4553 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329449 | 195373 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QU | NP441QU | np44 1qu | np441qu | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4553 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329449 | 195373 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QW | NP441QW | np44 1qw | np441qw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4486 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329545 | 195860 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QX | NP441QX | np44 1qx | np441qx | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4302 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329750 | 196010 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1QZ | NP441QZ | np44 1qz | np441qz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5033 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329187 | 196815 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RA | NP441RA | np44 1ra | np441ra | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5075 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329140 | 196804 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RB | NP441RB | np44 1rb | np441rb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4912 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329264 | 196648 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RD | NP441RD | np44 1rd | np441rd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4980 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329220 | 196741 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RE | NP441RE | np44 1re | np441re | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5017 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329134 | 196566 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RF | NP441RF | np44 1rf | np441rf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5018 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329167 | 196695 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RG | NP441RG | np44 1rg | np441rg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4866 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329320 | 196675 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RH | NP441RH | np44 1rh | np441rh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4883 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329362 | 196873 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RJ | NP441RJ | np44 1rj | np441rj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4919 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329297 | 196785 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RL | NP441RL | np44 1rl | np441rl | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4959 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329295 | 196910 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RN | NP441RN | np44 1rn | np441rn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5024 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329209 | 196858 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RP | NP441RP | np44 1rp | np441rp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4912 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329355 | 196942 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RQ | NP441RQ | np44 1rq | np441rq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4888 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329335 | 196805 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RR | NP441RR | np44 1rr | np441rr | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5035 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329173 | 196775 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RS | NP441RS | np44 1rs | np441rs | Torfaen | Tor-Faen | Pantygasseg WwTW | 5090 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328993 | 196618 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RT | NP441RT | np44 1rt | np441rt | Torfaen | Tor-Faen | Pantygasseg WwTW | 5036 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329040 | 196760 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RU | NP441RU | np44 1ru | np441ru | Torfaen | Tor-Faen | Pantygasseg WwTW | 4980 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328901 | 196679 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RW | NP441RW | np44 1rw | np441rw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5018 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329252 | 196968 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RX | NP441RX | np44 1rx | np441rx | Torfaen | Tor-Faen | Pantygasseg WwTW | 5041 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329159 | 196906 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RY | NP441RY | np44 1ry | np441ry | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5092 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329081 | 196660 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1RZ | NP441RZ | np44 1rz | np441rz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4972 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328998 | 196810 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1SA | NP441SA | np44 1sa | np441sa | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4838 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329468 | 197039 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1SB | NP441SB | np44 1sb | np441sb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4826 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329543 | 197196 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1SD | NP441SD | np44 1sd | np441sd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4856 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329467 | 197087 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1SE | NP441SE | np44 1se | np441se | Torfaen | Tor-Faen | Pantygasseg WwTW | 4954 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328915 | 196737 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1SF | NP441SF | np44 1sf | np441sf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4921 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 328876 | 196741 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1SG | NP441SG | np44 1sg | np441sg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4906 | 1366 | 1200to1500 | 2.73 | 2 | 1.47 | 25.46 | 13.58 | 15.01 | 329449 | 197178 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1SN | NP441SN | np44 1sn | np441sn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4236 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328076 | 196884 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1SR | NP441SR | np44 1sr | np441sr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4375 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328203 | 196814 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1SS | NP441SS | np44 1ss | np441ss | Torfaen | Tor-Faen | Pantygasseg WwTW | 4301 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328165 | 196881 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1SY | NP441SY | np44 1sy | np441sy | Torfaen | Tor-Faen | Pantygasseg WwTW | 4485 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328329 | 196785 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1SZ | NP441SZ | np44 1sz | np441sz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4448 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328315 | 196824 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1TA | NP441TA | np44 1ta | np441ta | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4779 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329571 | 197140 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1TB | NP441TB | np44 1tb | np441tb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4690 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329645 | 197086 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1TS | NP441TS | np44 1ts | np441ts | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4720 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329502 | 196774 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1TT | NP441TT | np44 1tt | np441tt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4375 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329718 | 196240 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1TX | NP441TX | np44 1tx | np441tx | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4504 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329615 | 196372 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1TY | NP441TY | np44 1ty | np441ty | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4592 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329616 | 196712 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1TZ | NP441TZ | np44 1tz | np441tz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4563 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329744 | 196991 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1UA | NP441UA | np44 1ua | np441ua | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4563 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329765 | 197045 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1UB | NP441UB | np44 1ub | np441ub | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4552 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329731 | 196925 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1UD | NP441UD | np44 1ud | np441ud | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4670 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329693 | 197150 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1UE | NP441UE | np44 1ue | np441ue | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4365 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329725 | 196222 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1UF | NP441UF | np44 1uf | np441uf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4564 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329590 | 196520 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1UG | NP441UG | np44 1ug | np441ug | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4496 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329687 | 196615 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1UH | NP441UH | np44 1uh | np441uh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4474 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329682 | 196515 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1UL | NP441UL | np44 1ul | np441ul | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4830 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329172 | 195386 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1UU | NP441UU | np44 1uu | np441uu | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4473 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329668 | 196459 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1XE | NP441XE | np44 1xe | np441xe | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4665 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329501 | 196578 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1XF | NP441XF | np44 1xf | np441xf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4588 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329420 | 195598 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1XG | NP441XG | np44 1xg | np441xg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4585 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329417 | 195306 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1XH | NP441XH | np44 1xh | np441xh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4224 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329864 | 196199 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1XL | NP441XL | np44 1xl | np441xl | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4495 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329509 | 195486 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1XN | NP441XN | np44 1xn | np441xn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4499 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329509 | 195588 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1XP | NP441XP | np44 1xp | np441xp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4506 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329502 | 195591 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1XQ | NP441XQ | np44 1xq | np441xq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4485 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329518 | 195451 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1XY | NP441XY | np44 1xy | np441xy | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4630 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329644 | 196914 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1YA | NP441YA | np44 1ya | np441ya | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4347 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329739 | 196202 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1YE | NP441YE | np44 1ye | np441ye | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1YN | NP441YN | np44 1yn | np441yn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4670 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329332 | 195295 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1YS | NP441YS | np44 1ys | np441ys | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4511 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329491 | 195355 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1YU | NP441YU | np44 1yu | np441yu | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4492 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329512 | 195493 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1YW | NP441YW | np44 1yw | np441yw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4493 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329510 | 195473 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 1YX | NP441YX | np44 1yx | np441yx | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4512 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329490 | 195386 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AG | NP442AG | np44 2ag | np442ag | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3274 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330733 | 195156 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AH | NP442AH | np44 2ah | np442ah | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3397 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330620 | 195682 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AL | NP442AL | np44 2al | np442al | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3346 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330679 | 195748 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AN | NP442AN | np44 2an | np442an | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3264 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330753 | 195672 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AP | NP442AP | np44 2ap | np442ap | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3314 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330712 | 195756 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AQ | NP442AQ | np44 2aq | np442aq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3336 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330665 | 195377 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AR | NP442AR | np44 2ar | np442ar | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3286 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330740 | 195756 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AS | NP442AS | np44 2as | np442as | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3076 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330958 | 195796 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AT | NP442AT | np44 2at | np442at | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3143 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330898 | 195847 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AU | NP442AU | np44 2au | np442au | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3144 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330893 | 195822 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AW | NP442AW | np44 2aw | np442aw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3144 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330881 | 195741 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AX | NP442AX | np44 2ax | np442ax | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3172 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330863 | 195812 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AY | NP442AY | np44 2ay | np442ay | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3133 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330925 | 195946 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2AZ | NP442AZ | np44 2az | np442az | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3293 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330781 | 196037 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2BA | NP442BA | np44 2ba | np442ba | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3199 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330836 | 195814 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2BB | NP442BB | np44 2bb | np442bb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3203 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330840 | 195866 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2BD | NP442BD | np44 2bd | np442bd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3237 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330796 | 195805 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2BE | NP442BE | np44 2be | np442be | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3239 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330810 | 195907 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2BG | NP442BG | np44 2bg | np442bg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3416 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330619 | 195833 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2BH | NP442BH | np44 2bh | np442bh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3331 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330703 | 195819 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2BJ | NP442BJ | np44 2bj | np442bj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3457 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330545 | 195441 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2BL | NP442BL | np44 2bl | np442bl | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3245 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330862 | 196171 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2BQ | NP442BQ | np44 2bq | np442bq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3348 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330708 | 195954 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2BY | NP442BY | np44 2by | np442by | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 3819 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 331442 | 198184 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP44 2BZ | NP442BZ | np44 2bz | np442bz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3627 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 330833 | 197115 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2DA | NP442DA | np44 2da | np442da | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3870 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330191 | 196029 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2DB | NP442DB | np44 2db | np442db | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 3134 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 331786 | 197567 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP44 2DE | NP442DE | np44 2de | np442de | Monmouthshire | Sir Fynwy | Llandegfedd (Waunypwll) STW | 1822 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 332457 | 196317 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP44 2DF | NP442DF | np44 2df | np442df | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 2521 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 331494 | 195617 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2DT | NP442DT | np44 2dt | np442dt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3781 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330244 | 195777 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2DU | NP442DU | np44 2du | np442du | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3712 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330329 | 195892 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2DW | NP442DW | np44 2dw | np442dw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4055 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330027 | 196156 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2DX | NP442DX | np44 2dx | np442dx | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3566 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330460 | 195769 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2DY | NP442DY | np44 2dy | np442dy | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3983 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330086 | 196083 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2DZ | NP442DZ | np44 2dz | np442dz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3852 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330202 | 195982 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EA | NP442EA | np44 2ea | np442ea | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3510 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330524 | 195830 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EB | NP442EB | np44 2eb | np442eb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3544 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330511 | 195966 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2ED | NP442ED | np44 2ed | np442ed | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3659 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330402 | 196011 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EE | NP442EE | np44 2ee | np442ee | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3563 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330481 | 195900 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EF | NP442EF | np44 2ef | np442ef | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3595 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330465 | 195997 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EG | NP442EG | np44 2eg | np442eg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3655 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330392 | 195924 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EH | NP442EH | np44 2eh | np442eh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3754 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330320 | 196084 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EJ | NP442EJ | np44 2ej | np442ej | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3787 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330267 | 195978 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EL | NP442EL | np44 2el | np442el | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3793 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330278 | 196072 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EN | NP442EN | np44 2en | np442en | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3514 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330553 | 196026 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EP | NP442EP | np44 2ep | np442ep | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3419 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330626 | 195897 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EQ | NP442EQ | np44 2eq | np442eq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3699 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330366 | 196031 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2ER | NP442ER | np44 2er | np442er | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3414 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330646 | 195980 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2ES | NP442ES | np44 2es | np442es | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3438 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330632 | 196032 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2ET | NP442ET | np44 2et | np442et | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3465 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330610 | 196061 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EU | NP442EU | np44 2eu | np442eu | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3539 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330562 | 196185 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EW | NP442EW | np44 2ew | np442ew | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3649 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330432 | 196109 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EX | NP442EX | np44 2ex | np442ex | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3429 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330663 | 196136 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EY | NP442EY | np44 2ey | np442ey | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3534 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330550 | 196112 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2EZ | NP442EZ | np44 2ez | np442ez | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3636 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330453 | 196146 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2HA | NP442HA | np44 2ha | np442ha | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3625 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330502 | 196296 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2HB | NP442HB | np44 2hb | np442hb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3509 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330598 | 196206 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2HD | NP442HD | np44 2hd | np442hd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3377 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330688 | 196002 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2HE | NP442HE | np44 2he | np442he | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3498 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330658 | 196378 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2HF | NP442HF | np44 2hf | np442hf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3346 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330749 | 196135 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2HG | NP442HG | np44 2hg | np442hg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3789 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330244 | 195839 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2HH | NP442HH | np44 2hh | np442hh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3462 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330573 | 195830 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2HJ | NP442HJ | np44 2hj | np442hj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3533 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330617 | 196365 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2HL | NP442HL | np44 2hl | np442hl | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3484 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330664 | 196350 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2HN | NP442HN | np44 2hn | np442hn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3462 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330585 | 195912 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2HP | NP442HP | np44 2hp | np442hp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3394 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330688 | 196084 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JA | NP442JA | np44 2ja | np442ja | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4041 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330077 | 196315 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JB | NP442JB | np44 2jb | np442jb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4133 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330002 | 196391 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JD | NP442JD | np44 2jd | np442jd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4061 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330096 | 196462 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JE | NP442JE | np44 2je | np442je | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4146 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330046 | 196594 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JF | NP442JF | np44 2jf | np442jf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4104 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330069 | 196523 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JG | NP442JG | np44 2jg | np442jg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4280 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329881 | 196508 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JH | NP442JH | np44 2jh | np442jh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4211 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329975 | 196584 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JJ | NP442JJ | np44 2jj | np442jj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4070 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329962 | 195851 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JL | NP442JL | np44 2jl | np442jl | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4120 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329977 | 196233 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JU | NP442JU | np44 2ju | np442ju | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4164 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329877 | 195924 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JW | NP442JW | np44 2jw | np442jw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4225 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329834 | 196047 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JX | NP442JX | np44 2jx | np442jx | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4109 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329970 | 196147 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2JZ | NP442JZ | np44 2jz | np442jz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4114 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329960 | 196117 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LB | NP442LB | np44 2lb | np442lb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3821 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330271 | 196176 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LD | NP442LD | np44 2ld | np442ld | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3917 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330160 | 196115 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LE | NP442LE | np44 2le | np442le | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3691 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330415 | 196222 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LF | NP442LF | np44 2lf | np442lf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3805 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330279 | 196137 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LG | NP442LG | np44 2lg | np442lg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3889 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330202 | 196178 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LH | NP442LH | np44 2lh | np442lh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3932 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330205 | 196375 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LJ | NP442LJ | np44 2lj | np442lj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3831 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330285 | 196279 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LL | NP442LL | np44 2ll | np442ll | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3953 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330213 | 196479 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LN | NP442LN | np44 2ln | np442ln | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3688 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330446 | 196331 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LP | NP442LP | np44 2lp | np442lp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3747 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330373 | 196284 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LQ | NP442LQ | np44 2lq | np442lq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3875 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330239 | 196279 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LR | NP442LR | np44 2lr | np442lr | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3754 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330386 | 196361 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LS | NP442LS | np44 2ls | np442ls | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3960 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330185 | 196405 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LT | NP442LT | np44 2lt | np442lt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3979 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330120 | 196227 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LU | NP442LU | np44 2lu | np442lu | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4005 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330153 | 196460 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LW | NP442LW | np44 2lw | np442lw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3738 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 330512 | 196690 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LX | NP442LX | np44 2lx | np442lx | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3683 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330484 | 196442 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2LY | NP442LY | np44 2ly | np442ly | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3966 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330118 | 196153 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NA | NP442NA | np44 2na | np442na | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3868 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330469 | 196925 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NB | NP442NB | np44 2nb | np442nb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3639 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330545 | 196489 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2ND | NP442ND | np44 2nd | np442nd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3858 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330445 | 196845 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NE | NP442NE | np44 2ne | np442ne | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3787 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330478 | 196739 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NF | NP442NF | np44 2nf | np442nf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3702 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 330528 | 196630 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NG | NP442NG | np44 2ng | np442ng | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3758 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330469 | 196632 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NH | NP442NH | np44 2nh | np442nh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3771 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 330539 | 196845 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NJ | NP442NJ | np44 2nj | np442nj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3898 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330346 | 196703 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NL | NP442NL | np44 2nl | np442nl | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3903 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330313 | 196626 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NN | NP442NN | np44 2nn | np442nn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3853 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330366 | 196628 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NP | NP442NP | np44 2np | np442np | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3949 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330258 | 196607 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NQ | NP442NQ | np44 2nq | np442nq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3693 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 330509 | 196552 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NR | NP442NR | np44 2nr | np442nr | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3959 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330235 | 196569 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NS | NP442NS | np44 2ns | np442ns | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3752 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330441 | 196533 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NT | NP442NT | np44 2nt | np442nt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3873 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330308 | 196516 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NU | NP442NU | np44 2nu | np442nu | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3813 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330375 | 196529 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NW | NP442NW | np44 2nw | np442nw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3861 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330400 | 196742 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NX | NP442NX | np44 2nx | np442nx | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3646 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 330591 | 196639 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NY | NP442NY | np44 2ny | np442ny | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3596 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 330666 | 196694 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2NZ | NP442NZ | np44 2nz | np442nz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3433 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330764 | 196492 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PB | NP442PB | np44 2pb | np442pb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3336 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330791 | 196258 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PD | NP442PD | np44 2pd | np442pd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3678 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 330611 | 196776 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PE | NP442PE | np44 2pe | np442pe | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3566 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 330642 | 196545 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PF | NP442PF | np44 2pf | np442pf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3498 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 330700 | 196507 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PG | NP442PG | np44 2pg | np442pg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3378 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330746 | 196252 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PH | NP442PH | np44 2ph | np442ph | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3351 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330800 | 196342 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PN | NP442PN | np44 2pn | np442pn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4361 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330036 | 197164 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PP | NP442PP | np44 2pp | np442pp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4494 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329950 | 197294 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PQ | NP442PQ | np44 2pq | np442pq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4384 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330034 | 197214 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PR | NP442PR | np44 2pr | np442pr | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4281 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330081 | 197069 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PT | NP442PT | np44 2pt | np442pt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4182 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330157 | 196996 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PU | NP442PU | np44 2pu | np442pu | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4063 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330258 | 196929 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PW | NP442PW | np44 2pw | np442pw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4069 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330271 | 196974 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PX | NP442PX | np44 2px | np442px | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4111 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330175 | 196854 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PY | NP442PY | np44 2py | np442py | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4179 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330119 | 196897 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2PZ | NP442PZ | np44 2pz | np442pz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4072 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330230 | 196885 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QA | NP442QA | np44 2qa | np442qa | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3995 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330311 | 196880 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QB | NP442QB | np44 2qb | np442qb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4025 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330186 | 196632 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QD | NP442QD | np44 2qd | np442qd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4307 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330008 | 196964 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QE | NP442QE | np44 2qe | np442qe | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4174 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330073 | 196761 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QF | NP442QF | np44 2qf | np442qf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4279 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330001 | 196867 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QG | NP442QG | np44 2qg | np442qg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4161 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330067 | 196705 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QH | NP442QH | np44 2qh | np442qh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4351 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330014 | 197091 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QJ | NP442QJ | np44 2qj | np442qj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4051 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330197 | 196743 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QL | NP442QL | np44 2ql | np442ql | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4102 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330146 | 196750 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QN | NP442QN | np44 2qn | np442qn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4279 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329923 | 196644 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QP | NP442QP | np44 2qp | np442qp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4249 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330000 | 196779 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QQ | NP442QQ | np44 2qq | np442qq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4288 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329971 | 196813 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QR | NP442QR | np44 2qr | np442qr | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4331 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329925 | 196813 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QS | NP442QS | np44 2qs | np442qs | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4311 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329981 | 196905 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QT | NP442QT | np44 2qt | np442qt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4329 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329960 | 196901 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QU | NP442QU | np44 2qu | np442qu | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4375 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329944 | 196987 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QW | NP442QW | np44 2qw | np442qw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4327 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 329902 | 196734 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QX | NP442QX | np44 2qx | np442qx | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4287 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330032 | 196969 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2QY | NP442QY | np44 2qy | np442qy | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4073 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 330127 | 196606 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2XJ | NP442XJ | np44 2xj | np442xj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3194 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330808 | 195278 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2YA | NP442YA | np44 2ya | np442ya | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3478 | 1253 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.35 | 12.46 | 13.77 | 330533 | 195612 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2YB | NP442YB | np44 2yb | np442yb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3526 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 330489 | 195658 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2YN | NP442YN | np44 2yn | np442yn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2YP | NP442YP | np44 2yp | np442yp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4258 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 329834 | 196222 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2YQ | NP442YQ | np44 2yq | np442yq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4737 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 329932 | 197774 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 2ZA | NP442ZA | np44 2za | np442za | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3207 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330796 | 195459 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AA | NP443AA | np44 3aa | np443aa | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5026 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328987 | 195690 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AB | NP443AB | np44 3ab | np443ab | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3326 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330412 | 193073 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AD | NP443AD | np44 3ad | np443ad | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5417 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328590 | 195580 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AE | NP443AE | np44 3ae | np443ae | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3723 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330239 | 192093 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AF | NP443AF | np44 3af | np443af | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3715 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330213 | 192188 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AG | NP443AG | np44 3ag | np443ag | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5468 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328536 | 195507 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AH | NP443AH | np44 3ah | np443ah | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5363 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328642 | 195545 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AJ | NP443AJ | np44 3aj | np443aj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5293 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328709 | 195294 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AL | NP443AL | np44 3al | np443al | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5054 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328953 | 195112 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AN | NP443AN | np44 3an | np443an | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4966 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329014 | 194990 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AP | NP443AP | np44 3ap | np443ap | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3842 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330028 | 192352 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AQ | NP443AQ | np44 3aq | np443aq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3808 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330110 | 192202 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AR | NP443AR | np44 3ar | np443ar | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5290 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328648 | 194906 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AS | NP443AS | np44 3as | np443as | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3840 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329980 | 194273 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AU | NP443AU | np44 3au | np443au | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4167 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 329555 | 193344 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AW | NP443AW | np44 3aw | np443aw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3936 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 329785 | 193392 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AX | NP443AX | np44 3ax | np443ax | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4189 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329536 | 193572 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AY | NP443AY | np44 3ay | np443ay | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3677 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330172 | 192448 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3AZ | NP443AZ | np44 3az | np443az | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4290 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329477 | 194032 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BA | NP443BA | np44 3ba | np443ba | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5447 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328560 | 195575 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BB | NP443BB | np44 3bb | np443bb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3960 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329877 | 194360 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BD | NP443BD | np44 3bd | np443bd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3991 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329815 | 194225 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BE | NP443BE | np44 3be | np443be | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4100 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329742 | 194396 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BG | NP443BG | np44 3bg | np443bg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3772 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329998 | 194012 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BH | NP443BH | np44 3bh | np443bh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3671 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330076 | 193841 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BJ | NP443BJ | np44 3bj | np443bj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3273 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330455 | 193625 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BL | NP443BL | np44 3bl | np443bl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3229 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330494 | 193532 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BN | NP443BN | np44 3bn | np443bn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3056 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330665 | 193393 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BP | NP443BP | np44 3bp | np443bp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3025 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330702 | 193213 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BQ | NP443BQ | np44 3bq | np443bq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3488 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330256 | 193808 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BR | NP443BR | np44 3br | np443br | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2930 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330798 | 193205 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BS | NP443BS | np44 3bs | np443bs | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3429 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330304 | 193700 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BT | NP443BT | np44 3bt | np443bt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3511 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330211 | 193501 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BU | NP443BU | np44 3bu | np443bu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3678 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330048 | 193591 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BW | NP443BW | np44 3bw | np443bw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3084 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330637 | 193359 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BX | NP443BX | np44 3bx | np443bx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3682 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330050 | 193686 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BY | NP443BY | np44 3by | np443by | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3466 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330265 | 193664 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3BZ | NP443BZ | np44 3bz | np443bz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3492 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330233 | 193571 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DA | NP443DA | np44 3da | np443da | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3678 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330060 | 193761 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DB | NP443DB | np44 3db | np443db | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3752 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329984 | 193746 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DD | NP443DD | np44 3dd | np443dd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3607 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330171 | 194047 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DE | NP443DE | np44 3de | np443de | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3681 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330047 | 193630 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DF | NP443DF | np44 3df | np443df | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3608 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330125 | 193699 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DH | NP443DH | np44 3dh | np443dh | Torfaen | Tor-Faen | Pantygasseg WwTW | 5597 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328363 | 195353 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DJ | NP443DJ | np44 3dj | np443dj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3225 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330520 | 193016 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DL | NP443DL | np44 3dl | np443dl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4212 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329554 | 194020 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DN | NP443DN | np44 3dn | np443dn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4256 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329501 | 193962 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DP | NP443DP | np44 3dp | np443dp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4179 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329570 | 193888 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DQ | NP443DQ | np44 3dq | np443dq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5032 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328989 | 195792 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DR | NP443DR | np44 3dr | np443dr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4093 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329646 | 193791 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DS | NP443DS | np44 3ds | np443ds | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3847 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329893 | 193787 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DT | NP443DT | np44 3dt | np443dt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3836 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329901 | 193751 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DU | NP443DU | np44 3du | np443du | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3951 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329792 | 193826 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DW | NP443DW | np44 3dw | np443dw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4089 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329666 | 193936 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DX | NP443DX | np44 3dx | np443dx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3932 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329810 | 193810 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DY | NP443DY | np44 3dy | np443dy | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3901 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329832 | 193707 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3DZ | NP443DZ | np44 3dz | np443dz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3873 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329853 | 193591 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EA | NP443EA | np44 3ea | np443ea | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3816 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329913 | 193648 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EB | NP443EB | np44 3eb | np443eb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3957 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329768 | 193576 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3ED | NP443ED | np44 3ed | np443ed | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3989 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329746 | 193736 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EE | NP443EE | np44 3ee | np443ee | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2733 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 331166 | 192441 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EF | NP443EF | np44 3ef | np443ef | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4310 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329465 | 194090 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EG | NP443EG | np44 3eg | np443eg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4248 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329497 | 193860 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EH | NP443EH | np44 3eh | np443eh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3938 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329793 | 193683 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EJ | NP443EJ | np44 3ej | np443ej | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4026 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329713 | 193785 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EL | NP443EL | np44 3el | np443el | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4063 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329665 | 193642 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EN | NP443EN | np44 3en | np443en | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5504 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328469 | 195052 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EP | NP443EP | np44 3ep | np443ep | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4166 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329572 | 193777 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EQ | NP443EQ | np44 3eq | np443eq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4128 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329605 | 193725 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3ER | NP443ER | np44 3er | np443er | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5591 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328402 | 195128 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3ES | NP443ES | np44 3es | np443es | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5374 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328582 | 194978 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3ET | NP443ET | np44 3et | np443et | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5207 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328734 | 194904 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EU | NP443EU | np44 3eu | np443eu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2979 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330743 | 193475 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EW | NP443EW | np44 3ew | np443ew | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4882 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329128 | 195627 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EX | NP443EX | np44 3ex | np443ex | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4224 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329561 | 194137 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EY | NP443EY | np44 3ey | np443ey | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3854 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329906 | 193954 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3EZ | NP443EZ | np44 3ez | np443ez | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4124 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329648 | 194055 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FA | NP443FA | np44 3fa | np443fa | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5634 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328370 | 195197 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FB | NP443FB | np44 3fb | np443fb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5572 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328430 | 195313 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FD | NP443FD | np44 3fd | np443fd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3912 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 329837 | 192942 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FE | NP443FE | np44 3fe | np443fe | Torfaen | Tor-Faen | Pantygasseg WwTW | 5579 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328222 | 195278 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FF | NP443FF | np44 3ff | np443ff | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4449 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329429 | 194578 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FG | NP443FG | np44 3fg | np443fg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3350 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330372 | 193461 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FH | NP443FH | np44 3fh | np443fh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3225 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330497 | 193340 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FJ | NP443FJ | np44 3fj | np443fj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4270 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329504 | 194077 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FL | NP443FL | np44 3fl | np443fl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3249 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330473 | 193471 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FN | NP443FN | np44 3fn | np443fn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3155 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330568 | 193314 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FP | NP443FP | np44 3fp | np443fp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3818 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329930 | 193862 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FQ | NP443FQ | np44 3fq | np443fq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5341 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328662 | 195227 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FR | NP443FR | np44 3fr | np443fr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5439 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328566 | 195141 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FS | NP443FS | np44 3fs | np443fs | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4118 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 329710 | 194341 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FT | NP443FT | np44 3ft | np443ft | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3613 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330222 | 192512 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FU | NP443FU | np44 3fu | np443fu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4136 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329762 | 194604 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FW | NP443FW | np44 3fw | np443fw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3909 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 329814 | 193286 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FX | NP443FX | np44 3fx | np443fx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4529 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329392 | 194740 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3FZ | NP443FZ | np44 3fz | np443fz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3408 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330412 | 192595 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3GA | NP443GA | np44 3ga | np443ga | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3637 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330089 | 193216 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3GB | NP443GB | np44 3gb | np443gb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3495 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330396 | 192333 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3GD | NP443GD | np44 3gd | np443gd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3463 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330290 | 193878 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3GE | NP443GE | np44 3ge | np443ge | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3529 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330236 | 193965 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3GH | NP443GH | np44 3gh | np443gh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3222 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330504 | 193592 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HB | NP443HB | np44 3hb | np443hb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3836 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 329937 | 192782 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HD | NP443HD | np44 3hd | np443hd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3870 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 329891 | 192857 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HE | NP443HE | np44 3he | np443he | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3116 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330640 | 192944 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HF | NP443HF | np44 3hf | np443hf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3191 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330560 | 192973 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HG | NP443HG | np44 3hg | np443hg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3115 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330629 | 193032 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HH | NP443HH | np44 3hh | np443hh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2985 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330765 | 192998 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HJ | NP443HJ | np44 3hj | np443hj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2934 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330809 | 193053 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HL | NP443HL | np44 3hl | np443hl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3055 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330702 | 192945 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HN | NP443HN | np44 3hn | np443hn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3213 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330519 | 193147 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HP | NP443HP | np44 3hp | np443hp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3526 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330248 | 192802 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HQ | NP443HQ | np44 3hq | np443hq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3675 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330110 | 192729 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HR | NP443HR | np44 3hr | np443hr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3489 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330294 | 192755 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3HS | NP443HS | np44 3hs | np443hs | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2940 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330795 | 193122 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JA | NP443JA | np44 3ja | np443ja | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4676 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329170 | 194481 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JB | NP443JB | np44 3jb | np443jb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4544 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329361 | 194687 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JJ | NP443JJ | np44 3jj | np443jj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3133 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 330595 | 193206 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JL | NP443JL | np44 3jl | np443jl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4656 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329251 | 194711 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JN | NP443JN | np44 3jn | np443jn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4518 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329395 | 194710 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JP | NP443JP | np44 3jp | np443jp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4357 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329531 | 194604 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JQ | NP443JQ | np44 3jq | np443jq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5012 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328990 | 195429 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JR | NP443JR | np44 3jr | np443jr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4645 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329336 | 194941 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JS | NP443JS | np44 3js | np443js | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4603 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329337 | 194810 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JT | NP443JT | np44 3jt | np443jt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4595 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329322 | 194736 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JU | NP443JU | np44 3ju | np443ju | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4420 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329448 | 194537 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JW | NP443JW | np44 3jw | np443jw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4389 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329511 | 194647 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JX | NP443JX | np44 3jx | np443jx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4238 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329634 | 194528 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JY | NP443JY | np44 3jy | np443jy | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4495 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329433 | 194758 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3JZ | NP443JZ | np44 3jz | np443jz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4367 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329545 | 194685 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LA | NP443LA | np44 3la | np443la | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4275 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329653 | 194723 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LB | NP443LB | np44 3lb | np443lb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4618 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329266 | 194624 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LD | NP443LD | np44 3ld | np443ld | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4774 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329069 | 194478 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LE | NP443LE | np44 3le | np443le | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4607 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329254 | 194533 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LF | NP443LF | np44 3lf | np443lf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4693 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329163 | 194526 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LG | NP443LG | np44 3lg | np443lg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4682 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329205 | 194642 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LH | NP443LH | np44 3lh | np443lh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5171 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328860 | 195895 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LJ | NP443LJ | np44 3lj | np443lj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4755 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329120 | 194607 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LL | NP443LL | np44 3ll | np443ll | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5043 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328860 | 194751 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LN | NP443LN | np44 3ln | np443ln | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4884 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329130 | 195694 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LP | NP443LP | np44 3lp | np443lp | Torfaen | Tor-Faen | Pantygasseg WwTW | 5528 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328455 | 195507 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LQ | NP443LQ | np44 3lq | np443lq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4668 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329204 | 194586 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LR | NP443LR | np44 3lr | np443lr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4765 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329189 | 194879 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LS | NP443LS | np44 3ls | np443ls | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4839 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329139 | 194963 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LT | NP443LT | np44 3lt | np443lt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4779 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329137 | 194759 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LU | NP443LU | np44 3lu | np443lu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4810 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329065 | 194616 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LW | NP443LW | np44 3lw | np443lw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4865 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329017 | 194648 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LX | NP443LX | np44 3lx | np443lx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4855 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329074 | 194815 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LY | NP443LY | np44 3ly | np443ly | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4828 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329091 | 194776 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3LZ | NP443LZ | np44 3lz | np443lz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4925 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328964 | 194683 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NA | NP443NA | np44 3na | np443na | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5022 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328863 | 194679 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NB | NP443NB | np44 3nb | np443nb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4889 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329011 | 194720 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3ND | NP443ND | np44 3nd | np443nd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4931 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328974 | 194742 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NE | NP443NE | np44 3ne | np443ne | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4748 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329187 | 194817 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NF | NP443NF | np44 3nf | np443nf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5170 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328680 | 194555 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NG | NP443NG | np44 3ng | np443ng | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5149 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328726 | 194658 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NH | NP443NH | np44 3nh | np443nh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4933 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328986 | 194791 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NJ | NP443NJ | np44 3nj | np443nj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4964 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328969 | 194842 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NL | NP443NL | np44 3nl | np443nl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4998 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328863 | 194583 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NN | NP443NN | np44 3nn | np443nn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4918 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329032 | 194890 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NP | NP443NP | np44 3np | np443np | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5035 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328821 | 194567 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NQ | NP443NQ | np44 3nq | np443nq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5174 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328730 | 194772 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NR | NP443NR | np44 3nr | np443nr | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4850 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329170 | 195769 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NS | NP443NS | np44 3ns | np443ns | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4951 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329004 | 194913 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NU | NP443NU | np44 3nu | np443nu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5017 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328917 | 194855 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NW | NP443NW | np44 3nw | np443nw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5138 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328759 | 194739 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NX | NP443NX | np44 3nx | np443nx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5120 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328743 | 194604 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NY | NP443NY | np44 3ny | np443ny | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5017 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328934 | 194908 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3NZ | NP443NZ | np44 3nz | np443nz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4908 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329066 | 194963 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PA | NP443PA | np44 3pa | np443pa | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5041 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328835 | 194647 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PB | NP443PB | np44 3pb | np443pb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4548 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329457 | 195181 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PD | NP443PD | np44 3pd | np443pd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4742 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329268 | 195067 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PE | NP443PE | np44 3pe | np443pe | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4750 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329255 | 195175 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PF | NP443PF | np44 3pf | np443pf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4875 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328958 | 194446 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PG | NP443PG | np44 3pg | np443pg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4493 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329489 | 194918 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PJ | NP443PJ | np44 3pj | np443pj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4499 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329506 | 195185 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PP | NP443PP | np44 3pp | np443pp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4608 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329401 | 195094 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PQ | NP443PQ | np44 3pq | np443pq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4405 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329569 | 194880 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PR | NP443PR | np44 3pr | np443pr | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4625 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329387 | 195034 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PS | NP443PS | np44 3ps | np443ps | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4529 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329441 | 194889 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PT | NP443PT | np44 3pt | np443pt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4482 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329480 | 194857 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PU | NP443PU | np44 3pu | np443pu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4394 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329556 | 194808 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PW | NP443PW | np44 3pw | np443pw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4646 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329366 | 195044 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PX | NP443PX | np44 3px | np443px | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4480 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329515 | 194950 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3PZ | NP443PZ | np44 3pz | np443pz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4227 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329722 | 194779 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QA | NP443QA | np44 3qa | np443qa | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4466 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329546 | 195047 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QB | NP443QB | np44 3qb | np443qb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4536 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329478 | 195017 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QD | NP443QD | np44 3qd | np443qd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4467 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329543 | 195080 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QE | NP443QE | np44 3qe | np443qe | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4466 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329530 | 194951 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QF | NP443QF | np44 3qf | np443qf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4506 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329503 | 195098 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QG | NP443QG | np44 3qg | np443qg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4425 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329585 | 195084 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QH | NP443QH | np44 3qh | np443qh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4394 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329615 | 195093 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QJ | NP443QJ | np44 3qj | np443qj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4394 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329618 | 195052 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QL | NP443QL | np44 3ql | np443ql | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4393 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329620 | 195028 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QN | NP443QN | np44 3qn | np443qn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4373 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329628 | 194948 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QP | NP443QP | np44 3qp | np443qp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4395 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329620 | 194988 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QQ | NP443QQ | np44 3qq | np443qq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4398 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329602 | 194951 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QR | NP443QR | np44 3qr | np443qr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4333 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329643 | 194872 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QS | NP443QS | np44 3qs | np443qs | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4398 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329607 | 195172 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QT | NP443QT | np44 3qt | np443qt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4399 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329608 | 195127 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QU | NP443QU | np44 3qu | np443qu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4585 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329415 | 194984 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QW | NP443QW | np44 3qw | np443qw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4360 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329626 | 194906 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QX | NP443QX | np44 3qx | np443qx | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4567 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329442 | 195096 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QY | NP443QY | np44 3qy | np443qy | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4421 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329584 | 195180 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3QZ | NP443QZ | np44 3qz | np443qz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4421 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329584 | 195180 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3SE | NP443SE | np44 3se | np443se | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3854 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 329879 | 193105 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3UW | NP443UW | np44 3uw | np443uw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4042 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 329694 | 193063 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3WY | NP443WY | np44 3wy | np443wy | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4321 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329683 | 195191 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3WZ | NP443WZ | np44 3wz | np443wz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3403 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330323 | 193236 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3XB | NP443XB | np44 3xb | np443xb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3356 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330365 | 193396 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3XH | NP443XH | np44 3xh | np443xh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4588 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329415 | 195220 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3XQ | NP443XQ | np44 3xq | np443xq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5499 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328127 | 195310 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3XS | NP443XS | np44 3xs | np443xs | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3736 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 330015 | 192939 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3XU | NP443XU | np44 3xu | np443xu | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4291 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329711 | 195275 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3XX | NP443XX | np44 3xx | np443xx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4154 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329823 | 194845 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3YA | NP443YA | np44 3ya | np443ya | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4562 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329441 | 195217 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3YJ | NP443YJ | np44 3yj | np443yj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2623 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 331146 | 192912 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3YL | NP443YL | np44 3yl | np443yl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3042 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330684 | 193586 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3YR | NP443YR | np44 3yr | np443yr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4579 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 329358 | 194797 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3YS | NP443YS | np44 3ys | np443ys | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4385 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329419 | 194259 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 3ZG | NP443ZG | np44 3zg | np443zg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4AA | NP444AA | np44 4aa | np444aa | Torfaen | Tor-Faen | Pantygasseg WwTW | 5738 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328103 | 195012 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4AB | NP444AB | np44 4ab | np444ab | Torfaen | Tor-Faen | Pantygasseg WwTW | 5571 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327984 | 195135 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4AD | NP444AD | np44 4ad | np444ad | Torfaen | Tor-Faen | Pantygasseg WwTW | 5742 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328126 | 195022 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4AE | NP444AE | np44 4ae | np444ae | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5674 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328223 | 194807 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4AF | NP444AF | np44 4af | np444af | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5807 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328099 | 194859 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4BJ | NP444BJ | np44 4bj | np444bj | Torfaen | Tor-Faen | Pantygasseg WwTW | 5256 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327889 | 195447 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4BQ | NP444BQ | np44 4bq | np444bq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5329 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327929 | 195385 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DA | NP444DA | np44 4da | np444da | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5957 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327815 | 194179 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DB | NP444DB | np44 4db | np444db | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6033 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327741 | 194200 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DD | NP444DD | np44 4dd | np444dd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6083 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327688 | 194181 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DE | NP444DE | np44 4de | np444de | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5759 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328047 | 194393 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DF | NP444DF | np44 4df | np444df | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5821 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327987 | 194404 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DG | NP444DG | np44 4dg | np444dg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5786 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328016 | 194371 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DH | NP444DH | np44 4dh | np444dh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5972 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327796 | 194153 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DJ | NP444DJ | np44 4dj | np444dj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5885 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327889 | 194194 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DL | NP444DL | np44 4dl | np444dl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5839 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327935 | 194191 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DN | NP444DN | np44 4dn | np444dn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5785 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328011 | 194332 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DQ | NP444DQ | np44 4dq | np444dq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5798 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328002 | 194355 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DW | NP444DW | np44 4dw | np444dw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5885 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327912 | 194349 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DY | NP444DY | np44 4dy | np444dy | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5913 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327887 | 194364 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4DZ | NP444DZ | np44 4dz | np444dz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5929 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327877 | 194405 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4EE | NP444EE | np44 4ee | np444ee | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6010 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327795 | 194402 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4EF | NP444EF | np44 4ef | np444ef | Torfaen | Tor-Faen | Pantygasseg WwTW | 6081 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327720 | 194415 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4EG | NP444EG | np44 4eg | np444eg | Torfaen | Tor-Faen | Pantygasseg WwTW | 6090 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327677 | 194385 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4EH | NP444EH | np44 4eh | np444eh | Torfaen | Tor-Faen | Pantygasseg WwTW | 5899 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327169 | 194379 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4EJ | NP444EJ | np44 4ej | np444ej | Torfaen | Tor-Faen | Pantygasseg WwTW | 5887 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327110 | 194371 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4EN | NP444EN | np44 4en | np444en | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6050 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327733 | 194263 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4EQ | NP444EQ | np44 4eq | np444eq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6079 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327713 | 194331 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4EW | NP444EW | np44 4ew | np444ew | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6026 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327754 | 194246 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4EY | NP444EY | np44 4ey | np444ey | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5996 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327794 | 194310 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4EZ | NP444EZ | np44 4ez | np444ez | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6011 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327787 | 194362 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4HA | NP444HA | np44 4ha | np444ha | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5113 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328731 | 194523 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4HB | NP444HB | np44 4hb | np444hb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5401 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328445 | 194560 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4HE | NP444HE | np44 4he | np444he | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5888 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327905 | 194320 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4HF | NP444HF | np44 4hf | np444hf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5913 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327874 | 194282 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4HG | NP444HG | np44 4hg | np444hg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5802 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327984 | 194267 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4HN | NP444HN | np44 4hn | np444hn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5874 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327909 | 194251 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4HQ | NP444HQ | np44 4hq | np444hq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5853 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327927 | 194233 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4HW | NP444HW | np44 4hw | np444hw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5939 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327838 | 194218 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4JZ | NP444JZ | np44 4jz | np444jz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5130 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328794 | 194835 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LA | NP444LA | np44 4la | np444la | Torfaen | Tor-Faen | Pantygasseg WwTW | 5562 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328050 | 195186 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LB | NP444LB | np44 4lb | np444lb | Torfaen | Tor-Faen | Pantygasseg WwTW | 5468 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327949 | 195235 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LD | NP444LD | np44 4ld | np444ld | Torfaen | Tor-Faen | Pantygasseg WwTW | 5400 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327958 | 195320 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LE | NP444LE | np44 4le | np444le | Torfaen | Tor-Faen | Pantygasseg WwTW | 5503 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328038 | 195249 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LF | NP444LF | np44 4lf | np444lf | Torfaen | Tor-Faen | Pantygasseg WwTW | 5247 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327781 | 195391 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LG | NP444LG | np44 4lg | np444lg | Torfaen | Tor-Faen | Pantygasseg WwTW | 5350 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327861 | 195319 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LH | NP444LH | np44 4lh | np444lh | Torfaen | Tor-Faen | Pantygasseg WwTW | 5191 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327723 | 195422 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LJ | NP444LJ | np44 4lj | np444lj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5207 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328666 | 194657 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LL | NP444LL | np44 4ll | np444ll | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5255 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328655 | 194805 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LN | NP444LN | np44 4ln | np444ln | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5301 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328588 | 194729 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LP | NP444LP | np44 4lp | np444lp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5506 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328355 | 194638 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LQ | NP444LQ | np44 4lq | np444lq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5220 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328631 | 194563 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LR | NP444LR | np44 4lr | np444lr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5292 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328613 | 194789 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LS | NP444LS | np44 4ls | np444ls | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5362 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328537 | 194776 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LT | NP444LT | np44 4lt | np444lt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5222 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328703 | 194852 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LW | NP444LW | np44 4lw | np444lw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5388 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328473 | 194626 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LX | NP444LX | np44 4lx | np444lx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5573 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328263 | 194532 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LY | NP444LY | np44 4ly | np444ly | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5421 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328475 | 194774 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4LZ | NP444LZ | np44 4lz | np444lz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5489 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328392 | 194720 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NA | NP444NA | np44 4na | np444na | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5603 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328242 | 194580 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NB | NP444NB | np44 4nb | np444nb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5698 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328169 | 194689 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4ND | NP444ND | np44 4nd | np444nd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5689 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328198 | 194769 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NF | NP444NF | np44 4nf | np444nf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5573 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328304 | 194717 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NG | NP444NG | np44 4ng | np444ng | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5610 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328290 | 194812 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NH | NP444NH | np44 4nh | np444nh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5592 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328327 | 194881 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NJ | NP444NJ | np44 4nj | np444nj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5663 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328251 | 194872 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NL | NP444NL | np44 4nl | np444nl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5668 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328257 | 194914 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NN | NP444NN | np44 4nn | np444nn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5588 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328361 | 194985 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NP | NP444NP | np44 4np | np444np | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5673 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328264 | 194957 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NQ | NP444NQ | np44 4nq | np444nq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5569 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328331 | 194807 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NR | NP444NR | np44 4nr | np444nr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5620 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328345 | 195045 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NS | NP444NS | np44 4ns | np444ns | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5590 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328370 | 195025 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NT | NP444NT | np44 4nt | np444nt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5523 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328429 | 194986 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NU | NP444NU | np44 4nu | np444nu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5538 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328390 | 194906 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NW | NP444NW | np44 4nw | np444nw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5631 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328311 | 194967 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NX | NP444NX | np44 4nx | np444nx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5518 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328385 | 194810 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NY | NP444NY | np44 4ny | np444ny | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5549 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328368 | 194870 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4NZ | NP444NZ | np44 4nz | np444nz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5420 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328496 | 194846 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PA | NP444PA | np44 4pa | np444pa | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5416 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328495 | 194827 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PB | NP444PB | np44 4pb | np444pb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5306 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328613 | 194841 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PD | NP444PD | np44 4pd | np444pd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5501 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328421 | 194881 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PE | NP444PE | np44 4pe | np444pe | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5502 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328435 | 194935 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PF | NP444PF | np44 4pf | np444pf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5406 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328533 | 194926 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PG | NP444PG | np44 4pg | np444pg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5450 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328482 | 194910 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PH | NP444PH | np44 4ph | np444ph | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5215 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328666 | 194690 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PJ | NP444PJ | np44 4pj | np444pj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5249 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328607 | 194590 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PL | NP444PL | np44 4pl | np444pl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5205 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328653 | 194591 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PN | NP444PN | np44 4pn | np444pn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5668 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328165 | 194527 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PP | NP444PP | np44 4pp | np444pp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5657 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328175 | 194519 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PQ | NP444PQ | np44 4pq | np444pq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5888 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327545 | 194547 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PR | NP444PR | np44 4pr | np444pr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5741 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328082 | 194482 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PS | NP444PS | np44 4ps | np444ps | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5902 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327917 | 194476 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PW | NP444PW | np44 4pw | np444pw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5881 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327974 | 194653 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PX | NP444PX | np44 4px | np444px | Torfaen | Tor-Faen | Pantygasseg WwTW | 6016 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327787 | 194520 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PY | NP444PY | np44 4py | np444py | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5967 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327857 | 194509 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4PZ | NP444PZ | np44 4pz | np444pz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5888 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327939 | 194517 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QB | NP444QB | np44 4qb | np444qb | Torfaen | Tor-Faen | Pantygasseg WwTW | 5959 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327762 | 194571 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QD | NP444QD | np44 4qd | np444qd | Torfaen | Tor-Faen | Pantygasseg WwTW | 5883 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327795 | 194673 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QE | NP444QE | np44 4qe | np444qe | Torfaen | Tor-Faen | Pantygasseg WwTW | 5950 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327861 | 194632 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QF | NP444QF | np44 4qf | np444qf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6001 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327829 | 194541 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QG | NP444QG | np44 4qg | np444qg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5887 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327955 | 194591 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QH | NP444QH | np44 4qh | np444qh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5795 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328037 | 194536 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QJ | NP444QJ | np44 4qj | np444qj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5789 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328066 | 194644 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QL | NP444QL | np44 4ql | np444ql | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5863 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328011 | 194734 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QN | NP444QN | np44 4qn | np444qn | Torfaen | Tor-Faen | Pantygasseg WwTW | 5862 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327911 | 194758 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QP | NP444QP | np44 4qp | np444qp | Torfaen | Tor-Faen | Pantygasseg WwTW | 5874 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327811 | 194691 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QQ | NP444QQ | np44 4qq | np444qq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5932 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327892 | 194669 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QR | NP444QR | np44 4qr | np444qr | Torfaen | Tor-Faen | Pantygasseg WwTW | 5892 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327858 | 194696 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QS | NP444QS | np44 4qs | np444qs | Torfaen | Tor-Faen | Pantygasseg WwTW | 5755 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327771 | 194805 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QT | NP444QT | np44 4qt | np444qt | Torfaen | Tor-Faen | Pantygasseg WwTW | 5811 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327455 | 194591 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QU | NP444QU | np44 4qu | np444qu | Torfaen | Tor-Faen | Pantygasseg WwTW | 5700 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327335 | 194660 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QW | NP444QW | np44 4qw | np444qw | Torfaen | Tor-Faen | Pantygasseg WwTW | 5831 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327862 | 194767 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QX | NP444QX | np44 4qx | np444qx | Torfaen | Tor-Faen | Pantygasseg WwTW | 5757 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327449 | 194647 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QY | NP444QY | np44 4qy | np444qy | Torfaen | Tor-Faen | Pantygasseg WwTW | 5915 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327692 | 194586 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4QZ | NP444QZ | np44 4qz | np444qz | Torfaen | Tor-Faen | Pantygasseg WwTW | 5808 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327717 | 194718 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4RA | NP444RA | np44 4ra | np444ra | Torfaen | Tor-Faen | Pantygasseg WwTW | 5861 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327656 | 194629 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4RB | NP444RB | np44 4rb | np444rb | Torfaen | Tor-Faen | Pantygasseg WwTW | 5598 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327915 | 195063 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4RD | NP444RD | np44 4rd | np444rd | Torfaen | Tor-Faen | Pantygasseg WwTW | 5671 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327902 | 194972 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4RE | NP444RE | np44 4re | np444re | Torfaen | Tor-Faen | Pantygasseg WwTW | 5641 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327966 | 195043 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4RF | NP444RF | np44 4rf | np444rf | Torfaen | Tor-Faen | Pantygasseg WwTW | 5719 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328020 | 194984 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4RG | NP444RG | np44 4rg | np444rg | Torfaen | Tor-Faen | Pantygasseg WwTW | 5726 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328153 | 195057 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4RN | NP444RN | np44 4rn | np444rn | Torfaen | Tor-Faen | Pantygasseg WwTW | 5695 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328198 | 195123 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4RQ | NP444RQ | np44 4rq | np444rq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5691 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328107 | 195070 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4RR | NP444RR | np44 4rr | np444rr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5664 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328305 | 195066 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4RX | NP444RX | np44 4rx | np444rx | Torfaen | Tor-Faen | Pantygasseg WwTW | 5531 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327843 | 195099 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4RY | NP444RY | np44 4ry | np444ry | Torfaen | Tor-Faen | Pantygasseg WwTW | 5524 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327926 | 195155 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4RZ | NP444RZ | np44 4rz | np444rz | Torfaen | Tor-Faen | Pantygasseg WwTW | 5532 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327884 | 195121 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SA | NP444SA | np44 4sa | np444sa | Torfaen | Tor-Faen | Pantygasseg WwTW | 5456 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327848 | 195189 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SB | NP444SB | np44 4sb | np444sb | Torfaen | Tor-Faen | Pantygasseg WwTW | 5472 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327775 | 195129 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SE | NP444SE | np44 4se | np444se | Torfaen | Tor-Faen | Pantygasseg WwTW | 5356 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327771 | 195259 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SF | NP444SF | np44 4sf | np444sf | Torfaen | Tor-Faen | Pantygasseg WwTW | 5405 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327768 | 195201 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SG | NP444SG | np44 4sg | np444sg | Torfaen | Tor-Faen | Pantygasseg WwTW | 5268 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327680 | 195309 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SH | NP444SH | np44 4sh | np444sh | Torfaen | Tor-Faen | Pantygasseg WwTW | 5204 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327617 | 195347 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SJ | NP444SJ | np44 4sj | np444sj | Torfaen | Tor-Faen | Pantygasseg WwTW | 5368 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327633 | 195169 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SL | NP444SL | np44 4sl | np444sl | Torfaen | Tor-Faen | Pantygasseg WwTW | 5461 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327725 | 195113 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SN | NP444SN | np44 4sn | np444sn | Torfaen | Tor-Faen | Pantygasseg WwTW | 5552 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327818 | 195061 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SP | NP444SP | np44 4sp | np444sp | Torfaen | Tor-Faen | Pantygasseg WwTW | 5562 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327755 | 195015 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SQ | NP444SQ | np44 4sq | np444sq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5328 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327691 | 195246 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SR | NP444SR | np44 4sr | np444sr | Torfaen | Tor-Faen | Pantygasseg WwTW | 5518 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327676 | 195022 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SS | NP444SS | np44 4ss | np444ss | Torfaen | Tor-Faen | Pantygasseg WwTW | 5468 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327680 | 195081 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4ST | NP444ST | np44 4st | np444st | Torfaen | Tor-Faen | Pantygasseg WwTW | 5439 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327587 | 195065 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SU | NP444SU | np44 4su | np444su | Torfaen | Tor-Faen | Pantygasseg WwTW | 5517 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327642 | 195006 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SW | NP444SW | np44 4sw | np444sw | Torfaen | Tor-Faen | Pantygasseg WwTW | 5582 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327760 | 194995 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SX | NP444SX | np44 4sx | np444sx | Torfaen | Tor-Faen | Pantygasseg WwTW | 5575 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327665 | 194952 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SY | NP444SY | np44 4sy | np444sy | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5751 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328190 | 194981 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4SZ | NP444SZ | np44 4sz | np444sz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5812 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328080 | 194807 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TA | NP444TA | np44 4ta | np444ta | Torfaen | Tor-Faen | Pantygasseg WwTW | 5953 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327611 | 194505 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TB | NP444TB | np44 4tb | np444tb | Torfaen | Tor-Faen | Pantygasseg WwTW | 5297 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327656 | 195262 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TD | NP444TD | np44 4td | np444td | Torfaen | Tor-Faen | Pantygasseg WwTW | 5615 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327722 | 194937 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TE | NP444TE | np44 4te | np444te | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6212 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327527 | 193871 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TF | NP444TF | np44 4tf | np444tf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6281 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327466 | 193963 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TG | NP444TG | np44 4tg | np444tg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5924 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327839 | 194105 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TH | NP444TH | np44 4th | np444th | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5895 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327858 | 194014 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TJ | NP444TJ | np44 4tj | np444tj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5911 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327836 | 193956 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TL | NP444TL | np44 4tl | np444tl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5847 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327898 | 193925 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TN | NP444TN | np44 4tn | np444tn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5957 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327787 | 193922 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TP | NP444TP | np44 4tp | np444tp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5835 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327900 | 193796 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TQ | NP444TQ | np44 4tq | np444tq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5898 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327859 | 194051 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TR | NP444TR | np44 4tr | np444tr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5909 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327825 | 193791 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TS | NP444TS | np44 4ts | np444ts | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5974 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327761 | 193807 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TT | NP444TT | np44 4tt | np444tt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5970 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327787 | 194056 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TU | NP444TU | np44 4tu | np444tu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5820 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327910 | 193708 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TW | NP444TW | np44 4tw | np444tw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5826 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327914 | 193872 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TX | NP444TX | np44 4tx | np444tx | Torfaen | Tor-Faen | Pantygasseg WwTW | 5823 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327333 | 194525 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TY | NP444TY | np44 4ty | np444ty | Torfaen | Tor-Faen | Pantygasseg WwTW | 5711 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327717 | 194826 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4TZ | NP444TZ | np44 4tz | np444tz | Torfaen | Tor-Faen | Pantygasseg WwTW | 5904 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327590 | 194550 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4UA | NP444UA | np44 4ua | np444ua | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5531 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 328350 | 194726 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4UX | NP444UX | np44 4ux | np444ux | Torfaen | Tor-Faen | Pantygasseg WwTW | 5231 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327457 | 195233 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4UY | NP444UY | np44 4uy | np444uy | Torfaen | Tor-Faen | Pantygasseg WwTW | 5293 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327590 | 195231 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4UZ | NP444UZ | np44 4uz | np444uz | Torfaen | Tor-Faen | Pantygasseg WwTW | 5292 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 327522 | 195197 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 4YZ | NP444YZ | np44 4yz | np444yz | Torfaen | Tor-Faen | Pantygasseg WwTW | 5532 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327352 | 194850 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AA | NP445AA | np44 5aa | np445aa | Torfaen | Tor-Faen | Pantygasseg WwTW | 3594 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327521 | 197242 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AB | NP445AB | np44 5ab | np445ab | Torfaen | Tor-Faen | Pantygasseg WwTW | 3851 | 1646 | Over1500 | 3.29 | 2.41 | 1.77 | 30.68 | 16.36 | 18.08 | 327450 | 196849 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AD | NP445AD | np44 5ad | np445ad | Torfaen | Tor-Faen | Pantygasseg WwTW | 4043 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327599 | 196721 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AE | NP445AE | np44 5ae | np445ae | Torfaen | Tor-Faen | Pantygasseg WwTW | 3874 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327502 | 196860 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AF | NP445AF | np44 5af | np445af | Torfaen | Tor-Faen | Pantygasseg WwTW | 3935 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327568 | 196835 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AG | NP445AG | np44 5ag | np445ag | Torfaen | Tor-Faen | Pantygasseg WwTW | 3805 | 1646 | Over1500 | 3.29 | 2.41 | 1.77 | 30.68 | 16.36 | 18.08 | 327357 | 196837 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AJ | NP445AJ | np44 5aj | np445aj | Torfaen | Tor-Faen | Pantygasseg WwTW | 5225 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327942 | 195517 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AL | NP445AL | np44 5al | np445al | Torfaen | Tor-Faen | Pantygasseg WwTW | 4025 | 1646 | Over1500 | 3.29 | 2.41 | 1.77 | 30.68 | 16.36 | 18.08 | 327341 | 196557 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AN | NP445AN | np44 5an | np445an | Torfaen | Tor-Faen | Pantygasseg WwTW | 3901 | 1646 | Over1500 | 3.29 | 2.41 | 1.77 | 30.68 | 16.36 | 18.08 | 327497 | 196822 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AP | NP445AP | np44 5ap | np445ap | Torfaen | Tor-Faen | Pantygasseg WwTW | 5062 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327192 | 195293 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AQ | NP445AQ | np44 5aq | np445aq | Torfaen | Tor-Faen | Pantygasseg WwTW | 3803 | 1646 | Over1500 | 3.29 | 2.41 | 1.77 | 30.68 | 16.36 | 18.08 | 327218 | 196742 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AR | NP445AR | np44 5ar | np445ar | Torfaen | Tor-Faen | Pantygasseg WwTW | 4773 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327167 | 195600 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AS | NP445AS | np44 5as | np445as | Torfaen | Tor-Faen | Pantygasseg WwTW | 4133 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327430 | 196487 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AT | NP445AT | np44 5at | np445at | Torfaen | Tor-Faen | Pantygasseg WwTW | 3844 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 326837 | 196473 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AU | NP445AU | np44 5au | np445au | Torfaen | Tor-Faen | Pantygasseg WwTW | 4679 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327039 | 195644 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AW | NP445AW | np44 5aw | np445aw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4739 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327124 | 195617 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AX | NP445AX | np44 5ax | np445ax | Torfaen | Tor-Faen | Pantygasseg WwTW | 3907 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327626 | 196919 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AY | NP445AY | np44 5ay | np445ay | Torfaen | Tor-Faen | Pantygasseg WwTW | 3860 | 1646 | Over1500 | 3.29 | 2.41 | 1.77 | 30.68 | 16.36 | 18.08 | 327363 | 196773 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5AZ | NP445AZ | np44 5az | np445az | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5331 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328678 | 195629 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5BA | NP445BA | np44 5ba | np445ba | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5456 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328554 | 195651 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5BB | NP445BB | np44 5bb | np445bb | Torfaen | Tor-Faen | Pantygasseg WwTW | 5324 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328205 | 195576 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5BD | NP445BD | np44 5bd | np445bd | Torfaen | Tor-Faen | Pantygasseg WwTW | 5282 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328277 | 195681 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5BE | NP445BE | np44 5be | np445be | Torfaen | Tor-Faen | Pantygasseg WwTW | 5213 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328279 | 195769 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5BG | NP445BG | np44 5bg | np445bg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 5309 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 328705 | 195713 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5BH | NP445BH | np44 5bh | np445bh | Torfaen | Tor-Faen | Pantygasseg WwTW | 5321 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328417 | 195739 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5BJ | NP445BJ | np44 5bj | np445bj | Torfaen | Tor-Faen | Pantygasseg WwTW | 5337 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328128 | 195506 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5BL | NP445BL | np44 5bl | np445bl | Torfaen | Tor-Faen | Pantygasseg WwTW | 5406 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328297 | 195541 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5BN | NP445BN | np44 5bn | np445bn | Torfaen | Tor-Faen | Pantygasseg WwTW | 5088 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326832 | 195119 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5BP | NP445BP | np44 5bp | np445bp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4985 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326841 | 195232 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5BR | NP445BR | np44 5br | np445br | Torfaen | Tor-Faen | Pantygasseg WwTW | 5223 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328401 | 195852 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5EA | NP445EA | np44 5ea | np445ea | Torfaen | Tor-Faen | Pantygasseg WwTW | 5191 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327013 | 195078 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5EB | NP445EB | np44 5eb | np445eb | Torfaen | Tor-Faen | Pantygasseg WwTW | 5215 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327077 | 195077 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5ED | NP445ED | np44 5ed | np445ed | Torfaen | Tor-Faen | Pantygasseg WwTW | 4784 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327062 | 195539 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5EE | NP445EE | np44 5ee | np445ee | Torfaen | Tor-Faen | Pantygasseg WwTW | 4872 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327082 | 195452 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5EF | NP445EF | np44 5ef | np445ef | Torfaen | Tor-Faen | Pantygasseg WwTW | 4931 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326986 | 195347 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5EG | NP445EG | np44 5eg | np445eg | Torfaen | Tor-Faen | Pantygasseg WwTW | 5011 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327019 | 195274 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5EJ | NP445EJ | np44 5ej | np445ej | Torfaen | Tor-Faen | Pantygasseg WwTW | 4914 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327167 | 195445 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5EP | NP445EP | np44 5ep | np445ep | Torfaen | Tor-Faen | Pantygasseg WwTW | 5007 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327170 | 195344 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HA | NP445HA | np44 5ha | np445ha | Torfaen | Tor-Faen | Pantygasseg WwTW | 5055 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327243 | 195324 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HB | NP445HB | np44 5hb | np445hb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4345 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328043 | 196702 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HD | NP445HD | np44 5hd | np445hd | Torfaen | Tor-Faen | Pantygasseg WwTW | 5039 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327305 | 195372 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HE | NP445HE | np44 5he | np445he | Torfaen | Tor-Faen | Pantygasseg WwTW | 5038 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327358 | 195399 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HF | NP445HF | np44 5hf | np445hf | Torfaen | Tor-Faen | Pantygasseg WwTW | 5011 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327332 | 195416 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HG | NP445HG | np44 5hg | np445hg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4960 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327240 | 195428 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HH | NP445HH | np44 5hh | np445hh | Torfaen | Tor-Faen | Pantygasseg WwTW | 5082 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327362 | 195352 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HJ | NP445HJ | np44 5hj | np445hj | Torfaen | Tor-Faen | Pantygasseg WwTW | 5155 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327241 | 195213 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HL | NP445HL | np44 5hl | np445hl | Torfaen | Tor-Faen | Pantygasseg WwTW | 5203 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327321 | 195197 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HN | NP445HN | np44 5hn | np445hn | Torfaen | Tor-Faen | Pantygasseg WwTW | 5168 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327349 | 195250 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HP | NP445HP | np44 5hp | np445hp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4248 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328017 | 196811 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HQ | NP445HQ | np44 5hq | np445hq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5150 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327390 | 195290 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HR | NP445HR | np44 5hr | np445hr | Torfaen | Tor-Faen | Pantygasseg WwTW | 5126 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327428 | 195336 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HS | NP445HS | np44 5hs | np445hs | Torfaen | Tor-Faen | Pantygasseg WwTW | 4268 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328008 | 196774 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HT | NP445HT | np44 5ht | np445ht | Torfaen | Tor-Faen | Pantygasseg WwTW | 4550 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328075 | 196457 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HU | NP445HU | np44 5hu | np445hu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4609 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328135 | 196431 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HW | NP445HW | np44 5hw | np445hw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4441 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328061 | 196589 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HX | NP445HX | np44 5hx | np445hx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4709 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328184 | 196341 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HY | NP445HY | np44 5hy | np445hy | Torfaen | Tor-Faen | Pantygasseg WwTW | 4213 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327978 | 196822 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5HZ | NP445HZ | np44 5hz | np445hz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4259 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327959 | 196742 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5JA | NP445JA | np44 5ja | np445ja | Torfaen | Tor-Faen | Pantygasseg WwTW | 4663 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328086 | 196318 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5JB | NP445JB | np44 5jb | np445jb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4634 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328107 | 196374 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5JE | NP445JE | np44 5je | np445je | Torfaen | Tor-Faen | Pantygasseg WwTW | 4410 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 328022 | 196596 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5JF | NP445JF | np44 5jf | np445jf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4513 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327989 | 196433 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5JQ | NP445JQ | np44 5jq | np445jq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4262 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327893 | 196680 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5LA | NP445LA | np44 5la | np445la | Torfaen | Tor-Faen | Pantygasseg WwTW | 4949 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326849 | 195274 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5LD | NP445LD | np44 5ld | np445ld | Torfaen | Tor-Faen | Pantygasseg WwTW | 4765 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328240 | 196315 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5LE | NP445LE | np44 5le | np445le | Torfaen | Tor-Faen | Pantygasseg WwTW | 4814 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328306 | 196308 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5LF | NP445LF | np44 5lf | np445lf | Torfaen | Tor-Faen | Pantygasseg WwTW | 5074 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328448 | 196087 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5LH | NP445LH | np44 5lh | np445lh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4797 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328245 | 196277 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5LJ | NP445LJ | np44 5lj | np445lj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4816 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328203 | 196216 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5LL | NP445LL | np44 5ll | np445ll | Torfaen | Tor-Faen | Pantygasseg WwTW | 4870 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 328298 | 196227 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SA | NP445SA | np44 5sa | np445sa | Torfaen | Tor-Faen | Pantygasseg WwTW | 4660 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327229 | 195757 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SB | NP445SB | np44 5sb | np445sb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4699 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327154 | 195676 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SD | NP445SD | np44 5sd | np445sd | Torfaen | Tor-Faen | Pantygasseg WwTW | 4656 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327116 | 195705 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SE | NP445SE | np44 5se | np445se | Torfaen | Tor-Faen | Pantygasseg WwTW | 4553 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327132 | 195828 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SF | NP445SF | np44 5sf | np445sf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4586 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327177 | 195813 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SG | NP445SG | np44 5sg | np445sg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4443 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327322 | 196054 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SH | NP445SH | np44 5sh | np445sh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4455 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327380 | 196074 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SJ | NP445SJ | np44 5sj | np445sj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4489 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327483 | 196097 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SL | NP445SL | np44 5sl | np445sl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4129 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327882 | 196847 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SN | NP445SN | np44 5sn | np445sn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4136 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327940 | 196892 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SP | NP445SP | np44 5sp | np445sp | Torfaen | Tor-Faen | Pantygasseg WwTW | 4622 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327933 | 196248 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SQ | NP445SQ | np44 5sq | np445sq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4522 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327866 | 196322 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SR | NP445SR | np44 5sr | np445sr | Torfaen | Tor-Faen | Pantygasseg WwTW | 4595 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327492 | 195978 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5ST | NP445ST | np44 5st | np445st | Torfaen | Tor-Faen | Pantygasseg WwTW | 3978 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327616 | 196818 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SU | NP445SU | np44 5su | np445su | Torfaen | Tor-Faen | Pantygasseg WwTW | 3882 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327535 | 196876 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SW | NP445SW | np44 5sw | np445sw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4033 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327775 | 196880 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5SX | NP445SX | np44 5sx | np445sx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4460 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327880 | 196412 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TA | NP445TA | np44 5ta | np445ta | Torfaen | Tor-Faen | Pantygasseg WwTW | 4351 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327805 | 196492 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TB | NP445TB | np44 5tb | np445tb | Torfaen | Tor-Faen | Pantygasseg WwTW | 4297 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327826 | 196578 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TD | NP445TD | np44 5td | np445td | Torfaen | Tor-Faen | Pantygasseg WwTW | 4353 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327942 | 196602 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TE | NP445TE | np44 5te | np445te | Torfaen | Tor-Faen | Pantygasseg WwTW | 4083 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327719 | 196767 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TF | NP445TF | np44 5tf | np445tf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4228 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327749 | 196604 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TG | NP445TG | np44 5tg | np445tg | Torfaen | Tor-Faen | Pantygasseg WwTW | 4177 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327717 | 196644 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TH | NP445TH | np44 5th | np445th | Torfaen | Tor-Faen | Pantygasseg WwTW | 4426 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327910 | 196480 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TJ | NP445TJ | np44 5tj | np445tj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4358 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327895 | 196556 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TL | NP445TL | np44 5tl | np445tl | Torfaen | Tor-Faen | Pantygasseg WwTW | 4420 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327976 | 196543 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TN | NP445TN | np44 5tn | np445tn | Torfaen | Tor-Faen | Pantygasseg WwTW | 4318 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327947 | 196652 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TQ | NP445TQ | np44 5tq | np445tq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4059 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 327682 | 196768 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TT | NP445TT | np44 5tt | np445tt | Torfaen | Tor-Faen | Pantygasseg WwTW | 4191 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327513 | 196474 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TU | NP445TU | np44 5tu | np445tu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4274 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327558 | 196404 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TW | NP445TW | np44 5tw | np445tw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4421 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327686 | 196315 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TX | NP445TX | np44 5tx | np445tx | Torfaen | Tor-Faen | Pantygasseg WwTW | 4365 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327582 | 196310 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TY | NP445TY | np44 5ty | np445ty | Torfaen | Tor-Faen | Pantygasseg WwTW | 4527 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327697 | 196192 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5TZ | NP445TZ | np44 5tz | np445tz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4663 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327442 | 195869 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UA | NP445UA | np44 5ua | np445ua | Torfaen | Tor-Faen | Pantygasseg WwTW | 4282 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327645 | 196457 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UB | NP445UB | np44 5ub | np445ub | Torfaen | Tor-Faen | Pantygasseg WwTW | 4497 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327569 | 196142 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UD | NP445UD | np44 5ud | np445ud | Torfaen | Tor-Faen | Pantygasseg WwTW | 4596 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327348 | 195893 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UE | NP445UE | np44 5ue | np445ue | Torfaen | Tor-Faen | Pantygasseg WwTW | 4684 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327327 | 195781 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UF | NP445UF | np44 5uf | np445uf | Torfaen | Tor-Faen | Pantygasseg WwTW | 4753 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327462 | 195777 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UG | NP445UG | np44 5ug | np445ug | Torfaen | Tor-Faen | Pantygasseg WwTW | 4800 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327444 | 195713 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UH | NP445UH | np44 5uh | np445uh | Torfaen | Tor-Faen | Pantygasseg WwTW | 4919 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327463 | 195588 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UJ | NP445UJ | np44 5uj | np445uj | Torfaen | Tor-Faen | Pantygasseg WwTW | 4950 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327609 | 195635 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UL | NP445UL | np44 5ul | np445ul | Torfaen | Tor-Faen | Pantygasseg WwTW | 5022 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327584 | 195537 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UN | NP445UN | np44 5un | np445un | Torfaen | Tor-Faen | Pantygasseg WwTW | 4992 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327716 | 195650 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UP | NP445UP | np44 5up | np445up | Torfaen | Tor-Faen | Pantygasseg WwTW | 4912 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327729 | 195752 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UQ | NP445UQ | np44 5uq | np445uq | Torfaen | Tor-Faen | Pantygasseg WwTW | 4814 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327623 | 195801 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UR | NP445UR | np44 5ur | np445ur | Torfaen | Tor-Faen | Pantygasseg WwTW | 4782 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327489 | 195759 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5US | NP445US | np44 5us | np445us | Torfaen | Tor-Faen | Pantygasseg WwTW | 4861 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327544 | 195700 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UT | NP445UT | np44 5ut | np445ut | Torfaen | Tor-Faen | Pantygasseg WwTW | 4408 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327486 | 196195 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UU | NP445UU | np44 5uu | np445uu | Torfaen | Tor-Faen | Pantygasseg WwTW | 4328 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327432 | 196255 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UW | NP445UW | np44 5uw | np445uw | Torfaen | Tor-Faen | Pantygasseg WwTW | 4286 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327430 | 196304 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UX | NP445UX | np44 5ux | np445ux | Torfaen | Tor-Faen | Pantygasseg WwTW | 4239 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327475 | 196389 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UY | NP445UY | np44 5uy | np445uy | Torfaen | Tor-Faen | Pantygasseg WwTW | 4335 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327508 | 196296 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5UZ | NP445UZ | np44 5uz | np445uz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4430 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 327574 | 196226 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5WA | NP445WA | np44 5wa | np445wa | Torfaen | Tor-Faen | Pantygasseg WwTW | 4589 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327412 | 195937 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5YY | NP445YY | np44 5yy | np445yy | Torfaen | Tor-Faen | Pantygasseg WwTW | 5313 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327158 | 195005 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 5YZ | NP445YZ | np44 5yz | np445yz | Torfaen | Tor-Faen | Pantygasseg WwTW | 4580 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 327439 | 195964 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EA | NP446EA | np44 6ea | np446ea | Torfaen | Tor-Faen | Pantygasseg WwTW | 6129 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 326347 | 193904 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EB | NP446EB | np44 6eb | np446eb | Torfaen | Tor-Faen | Pantygasseg WwTW | 6026 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 326401 | 194021 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6ED | NP446ED | np44 6ed | np446ed | Torfaen | Tor-Faen | Pantygasseg WwTW | 6272 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 326440 | 193778 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EE | NP446EE | np44 6ee | np446ee | Torfaen | Tor-Faen | Pantygasseg WwTW | 6117 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 326460 | 193941 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EH | NP446EH | np44 6eh | np446eh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6590 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 327133 | 193491 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EJ | NP446EJ | np44 6ej | np446ej | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6593 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327130 | 193533 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EL | NP446EL | np44 6el | np446el | Torfaen | Tor-Faen | Pantygasseg WwTW | 6597 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327076 | 193610 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EN | NP446EN | np44 6en | np446en | Torfaen | Tor-Faen | Pantygasseg WwTW | 6641 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326944 | 193525 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EP | NP446EP | np44 6ep | np446ep | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6561 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327165 | 193624 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EQ | NP446EQ | np44 6eq | np446eq | Torfaen | Tor-Faen | Pantygasseg WwTW | 6538 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326887 | 193616 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6ER | NP446ER | np44 6er | np446er | Torfaen | Tor-Faen | Pantygasseg WwTW | 6496 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326960 | 193681 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6ES | NP446ES | np44 6es | np446es | Torfaen | Tor-Faen | Pantygasseg WwTW | 6471 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326860 | 193678 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6ET | NP446ET | np44 6et | np446et | Torfaen | Tor-Faen | Pantygasseg WwTW | 6434 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326851 | 193714 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EU | NP446EU | np44 6eu | np446eu | Torfaen | Tor-Faen | Pantygasseg WwTW | 6570 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326965 | 193605 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EW | NP446EW | np44 6ew | np446ew | Torfaen | Tor-Faen | Pantygasseg WwTW | 6403 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326967 | 193780 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EX | NP446EX | np44 6ex | np446ex | Torfaen | Tor-Faen | Pantygasseg WwTW | 6347 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326895 | 193817 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EY | NP446EY | np44 6ey | np446ey | Torfaen | Tor-Faen | Pantygasseg WwTW | 5970 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 326463 | 194093 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6EZ | NP446EZ | np44 6ez | np446ez | Torfaen | Tor-Faen | Pantygasseg WwTW | 6042 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326685 | 194074 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HA | NP446HA | np44 6ha | np446ha | Torfaen | Tor-Faen | Pantygasseg WwTW | 6173 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326798 | 193970 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HB | NP446HB | np44 6hb | np446hb | Torfaen | Tor-Faen | Pantygasseg WwTW | 6257 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326555 | 193820 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HD | NP446HD | np44 6hd | np446hd | Torfaen | Tor-Faen | Pantygasseg WwTW | 6193 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326564 | 193887 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HE | NP446HE | np44 6he | np446he | Torfaen | Tor-Faen | Pantygasseg WwTW | 6525 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326689 | 193576 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HF | NP446HF | np44 6hf | np446hf | Torfaen | Tor-Faen | Pantygasseg WwTW | 6174 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327067 | 194052 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HG | NP446HG | np44 6hg | np446hg | Torfaen | Tor-Faen | Pantygasseg WwTW | 6270 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327040 | 193942 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HH | NP446HH | np44 6hh | np446hh | Torfaen | Tor-Faen | Pantygasseg WwTW | 6234 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326623 | 193860 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HJ | NP446HJ | np44 6hj | np446hj | Torfaen | Tor-Faen | Pantygasseg WwTW | 6017 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326738 | 194115 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HL | NP446HL | np44 6hl | np446hl | Torfaen | Tor-Faen | Pantygasseg WwTW | 5978 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326634 | 194127 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HN | NP446HN | np44 6hn | np446hn | Torfaen | Tor-Faen | Pantygasseg WwTW | 6371 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326690 | 193735 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HP | NP446HP | np44 6hp | np446hp | Torfaen | Tor-Faen | Pantygasseg WwTW | 5890 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 326480 | 194179 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HQ | NP446HQ | np44 6hq | np446hq | Torfaen | Tor-Faen | Pantygasseg WwTW | 6281 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326742 | 193842 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HR | NP446HR | np44 6hr | np446hr | Torfaen | Tor-Faen | Pantygasseg WwTW | 5791 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 326419 | 194266 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HS | NP446HS | np44 6hs | np446hs | Torfaen | Tor-Faen | Pantygasseg WwTW | 5775 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 326392 | 194276 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HT | NP446HT | np44 6ht | np446ht | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6724 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 326999 | 193307 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HU | NP446HU | np44 6hu | np446hu | Torfaen | Tor-Faen | Pantygasseg WwTW | 6610 | 1462 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.25 | 14.53 | 16.06 | 326234 | 193394 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HW | NP446HW | np44 6hw | np446hw | Torfaen | Tor-Faen | Pantygasseg WwTW | 6158 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 326436 | 193894 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HX | NP446HX | np44 6hx | np446hx | Torfaen | Tor-Faen | Pantygasseg WwTW | 6332 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326545 | 193740 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HY | NP446HY | np44 6hy | np446hy | Torfaen | Tor-Faen | Pantygasseg WwTW | 5638 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 326380 | 194414 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6HZ | NP446HZ | np44 6hz | np446hz | Torfaen | Tor-Faen | Pantygasseg WwTW | 6685 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 326510 | 193371 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JA | NP446JA | np44 6ja | np446ja | Torfaen | Tor-Faen | Pantygasseg WwTW | 5943 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326873 | 194232 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JB | NP446JB | np44 6jb | np446jb | Torfaen | Tor-Faen | Pantygasseg WwTW | 6253 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326591 | 193832 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JD | NP446JD | np44 6jd | np446jd | Torfaen | Tor-Faen | Pantygasseg WwTW | 5631 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326838 | 194548 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JE | NP446JE | np44 6je | np446je | Torfaen | Tor-Faen | Pantygasseg WwTW | 5490 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326800 | 194684 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JF | NP446JF | np44 6jf | np446jf | Torfaen | Tor-Faen | Pantygasseg WwTW | 5496 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326914 | 194716 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JG | NP446JG | np44 6jg | np446jg | Torfaen | Tor-Faen | Pantygasseg WwTW | 5386 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326846 | 194809 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JH | NP446JH | np44 6jh | np446jh | Torfaen | Tor-Faen | Pantygasseg WwTW | 5369 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326757 | 194797 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JJ | NP446JJ | np44 6jj | np446jj | Torfaen | Tor-Faen | Pantygasseg WwTW | 5703 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326975 | 194518 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JL | NP446JL | np44 6jl | np446jl | Torfaen | Tor-Faen | Pantygasseg WwTW | 5772 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326968 | 194443 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JN | NP446JN | np44 6jn | np446jn | Torfaen | Tor-Faen | Pantygasseg WwTW | 5347 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326656 | 194789 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JP | NP446JP | np44 6jp | np446jp | Torfaen | Tor-Faen | Pantygasseg WwTW | 5854 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327008 | 194370 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JQ | NP446JQ | np44 6jq | np446jq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5798 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326770 | 194352 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JR | NP446JR | np44 6jr | np446jr | Torfaen | Tor-Faen | Pantygasseg WwTW | 5916 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326782 | 194233 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JS | NP446JS | np44 6js | np446js | Torfaen | Tor-Faen | Pantygasseg WwTW | 5677 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326695 | 194456 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JT | NP446JT | np44 6jt | np446jt | Torfaen | Tor-Faen | Pantygasseg WwTW | 5614 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326614 | 194498 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JU | NP446JU | np44 6ju | np446ju | Torfaen | Tor-Faen | Pantygasseg WwTW | 5482 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326634 | 194641 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JW | NP446JW | np44 6jw | np446jw | Torfaen | Tor-Faen | Pantygasseg WwTW | 6659 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 326864 | 193484 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JX | NP446JX | np44 6jx | np446jx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6728 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 326994 | 193389 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JY | NP446JY | np44 6jy | np446jy | Torfaen | Tor-Faen | Pantygasseg WwTW | 5791 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326607 | 194313 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6JZ | NP446JZ | np44 6jz | np446jz | Torfaen | Tor-Faen | Pantygasseg WwTW | 6148 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326705 | 193970 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6LA | NP446LA | np44 6la | np446la | Torfaen | Tor-Faen | Pantygasseg WwTW | 5653 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 326856 | 194531 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6LB | NP446LB | np44 6lb | np446lb | Torfaen | Tor-Faen | Pantygasseg WwTW | 5947 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326725 | 194184 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6LD | NP446LD | np44 6ld | np446ld | Torfaen | Tor-Faen | Pantygasseg WwTW | 5764 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326879 | 194421 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6LE | NP446LE | np44 6le | np446le | Torfaen | Tor-Faen | Pantygasseg WwTW | 6131 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 326733 | 193995 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6TU | NP446TU | np44 6tu | np446tu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6009 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327719 | 193672 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6TY | NP446TY | np44 6ty | np446ty | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6231 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327498 | 193701 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6TZ | NP446TZ | np44 6tz | np446tz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6402 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327334 | 193823 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UA | NP446UA | np44 6ua | np446ua | Torfaen | Tor-Faen | Pantygasseg WwTW | 6165 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327329 | 194156 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UB | NP446UB | np44 6ub | np446ub | Torfaen | Tor-Faen | Pantygasseg WwTW | 6110 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327367 | 194230 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UD | NP446UD | np44 6ud | np446ud | Torfaen | Tor-Faen | Pantygasseg WwTW | 6001 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327169 | 194271 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UE | NP446UE | np44 6ue | np446ue | Torfaen | Tor-Faen | Pantygasseg WwTW | 6092 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327201 | 194186 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UF | NP446UF | np44 6uf | np446uf | Torfaen | Tor-Faen | Pantygasseg WwTW | 6042 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327275 | 194267 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UG | NP446UG | np44 6ug | np446ug | Torfaen | Tor-Faen | Pantygasseg WwTW | 6002 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327341 | 194336 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UH | NP446UH | np44 6uh | np446uh | Torfaen | Tor-Faen | Pantygasseg WwTW | 5917 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327227 | 194382 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UJ | NP446UJ | np44 6uj | np446uj | Torfaen | Tor-Faen | Pantygasseg WwTW | 5883 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327301 | 194448 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UL | NP446UL | np44 6ul | np446ul | Torfaen | Tor-Faen | Pantygasseg WwTW | 5809 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327245 | 194505 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UN | NP446UN | np44 6un | np446un | Torfaen | Tor-Faen | Pantygasseg WwTW | 5747 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327136 | 194529 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UP | NP446UP | np44 6up | np446up | Torfaen | Tor-Faen | Pantygasseg WwTW | 5637 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327198 | 194671 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UQ | NP446UQ | np44 6uq | np446uq | Torfaen | Tor-Faen | Pantygasseg WwTW | 5642 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327121 | 194636 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UR | NP446UR | np44 6ur | np446ur | Torfaen | Tor-Faen | Pantygasseg WwTW | 5704 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 327204 | 194602 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6US | NP446US | np44 6us | np446us | Torfaen | Tor-Faen | Pantygasseg WwTW | 6018 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327057 | 194213 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 6UT | NP446UT | np44 6ut | np446ut | Torfaen | Tor-Faen | Pantygasseg WwTW | 6030 | 1463 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.27 | 14.54 | 16.07 | 327118 | 194222 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AA | NP447AA | np44 7aa | np447aa | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5078 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328683 | 194040 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AB | NP447AB | np44 7ab | np447ab | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5013 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328741 | 193975 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AD | NP447AD | np44 7ad | np447ad | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4653 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329077 | 193684 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AE | NP447AE | np44 7ae | np447ae | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5407 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328342 | 193952 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AF | NP447AF | np44 7af | np447af | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5913 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 327809 | 193478 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AG | NP447AG | np44 7ag | np447ag | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5767 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327962 | 193686 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AH | NP447AH | np44 7ah | np447ah | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4659 | 1288 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.01 | 12.8 | 14.15 | 329063 | 193323 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AJ | NP447AJ | np44 7aj | np447aj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4531 | 1288 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.01 | 12.8 | 14.15 | 329191 | 193495 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AL | NP447AL | np44 7al | np447al | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4083 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 329665 | 192942 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AN | NP447AN | np44 7an | np447an | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4842 | 1246 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.22 | 12.39 | 13.69 | 329132 | 191869 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AP | NP447AP | np44 7ap | np447ap | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4555 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329176 | 193703 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AQ | NP447AQ | np44 7aq | np447aq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4720 | 1246 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.22 | 12.39 | 13.69 | 329115 | 192382 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AR | NP447AR | np44 7ar | np447ar | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5035 | 1246 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.22 | 12.39 | 13.69 | 328871 | 192062 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AS | NP447AS | np44 7as | np447as | Torfaen | Tor-Faen | Caerleon Road STW | 7697 | 1361 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.37 | 13.53 | 14.95 | 326262 | 191423 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AT | NP447AT | np44 7at | np447at | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6456 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 327270 | 193186 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AU | NP447AU | np44 7au | np447au | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 7033 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 326928 | 191593 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AW | NP447AW | np44 7aw | np447aw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4987 | 1246 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.22 | 12.39 | 13.69 | 329082 | 191581 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AX | NP447AX | np44 7ax | np447ax | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3693 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 330144 | 192493 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AY | NP447AY | np44 7ay | np447ay | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5445 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328296 | 193861 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7AZ | NP447AZ | np44 7az | np447az | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6168 | 1302 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.27 | 12.94 | 14.3 | 327643 | 192366 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7BA | NP447BA | np44 7ba | np447ba | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4668 | 1288 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.01 | 12.8 | 14.15 | 329054 | 193471 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7BB | NP447BB | np44 7bb | np447bb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3832 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 329977 | 192593 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7BE | NP447BE | np44 7be | np447be | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3904 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 329921 | 192517 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7DJ | NP447DJ | np44 7dj | np447dj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5578 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328206 | 194240 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7DP | NP447DP | np44 7dp | np447dp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5696 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328059 | 194026 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7DR | NP447DR | np44 7dr | np447dr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5606 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328136 | 193879 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7DS | NP447DS | np44 7ds | np447ds | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5554 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328189 | 193899 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7DT | NP447DT | np44 7dt | np447dt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5683 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328062 | 193921 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7DU | NP447DU | np44 7du | np447du | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5628 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328120 | 193949 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7DX | NP447DX | np44 7dx | np447dx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5523 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328227 | 193965 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7EA | NP447EA | np44 7ea | np447ea | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5494 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328250 | 193897 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7EB | NP447EB | np44 7eb | np447eb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5624 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328115 | 193854 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7ED | NP447ED | np44 7ed | np447ed | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5635 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328113 | 193955 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7EH | NP447EH | np44 7eh | np447eh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5647 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328088 | 193790 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7EL | NP447EL | np44 7el | np447el | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5458 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328307 | 194096 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7EU | NP447EU | np44 7eu | np447eu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5342 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328418 | 194051 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7EX | NP447EX | np44 7ex | np447ex | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5192 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328573 | 194081 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7EZ | NP447EZ | np44 7ez | np447ez | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4514 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329243 | 193974 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7GN | NP447GN | np44 7gn | np447gn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5268 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328561 | 194469 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HA | NP447HA | np44 7ha | np447ha | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4467 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329327 | 194210 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HB | NP447HB | np44 7hb | np447hb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4505 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329274 | 194126 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HD | NP447HD | np44 7hd | np447hd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4638 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329144 | 194158 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HE | NP447HE | np44 7he | np447he | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4500 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329294 | 194212 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HF | NP447HF | np44 7hf | np447hf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4417 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329322 | 193803 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HG | NP447HG | np44 7hg | np447hg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4753 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329026 | 194143 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HH | NP447HH | np44 7hh | np447hh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4664 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329112 | 194120 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HJ | NP447HJ | np44 7hj | np447hj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5073 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328703 | 194153 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HL | NP447HL | np44 7hl | np447hl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4962 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328822 | 194192 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HN | NP447HN | np44 7hn | np447hn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4974 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328823 | 194274 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HP | NP447HP | np44 7hp | np447hp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4762 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329040 | 194283 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HQ | NP447HQ | np44 7hq | np447hq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4845 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328936 | 194164 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HR | NP447HR | np44 7hr | np447hr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4797 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329024 | 194383 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HS | NP447HS | np44 7hs | np447hs | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4835 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328952 | 194205 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HT | NP447HT | np44 7ht | np447ht | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4918 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328901 | 194383 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HU | NP447HU | np44 7hu | np447hu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4977 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328844 | 194401 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HW | NP447HW | np44 7hw | np447hw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4871 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328923 | 194249 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HX | NP447HX | np44 7hx | np447hx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4836 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328968 | 194301 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HY | NP447HY | np44 7hy | np447hy | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5019 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328783 | 194303 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7HZ | NP447HZ | np44 7hz | np447hz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5035 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328750 | 194203 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JA | NP447JA | np44 7ja | np447ja | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5405 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328389 | 194291 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JB | NP447JB | np44 7jb | np447jb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5050 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328750 | 194294 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JD | NP447JD | np44 7jd | np447jd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5398 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328325 | 193534 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JE | NP447JE | np44 7je | np447je | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5475 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 328247 | 193484 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JF | NP447JF | np44 7jf | np447jf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5533 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328192 | 193595 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JG | NP447JG | np44 7jg | np447jg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5264 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328526 | 194252 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JH | NP447JH | np44 7jh | np447jh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5056 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328767 | 194416 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JJ | NP447JJ | np44 7jj | np447jj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5088 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328715 | 194315 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JL | NP447JL | np44 7jl | np447jl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5134 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328648 | 194194 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JN | NP447JN | np44 7jn | np447jn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5194 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328628 | 194424 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JP | NP447JP | np44 7jp | np447jp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5196 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328597 | 194265 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JQ | NP447JQ | np44 7jq | np447jq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5212 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328595 | 194348 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JR | NP447JR | np44 7jr | np447jr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5265 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328512 | 194168 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JS | NP447JS | np44 7js | np447js | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5580 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328243 | 194466 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JT | NP447JT | np44 7jt | np447jt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5347 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328467 | 194396 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JU | NP447JU | np44 7ju | np447ju | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5379 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328451 | 194482 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JW | NP447JW | np44 7jw | np447jw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5423 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328397 | 194437 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JX | NP447JX | np44 7jx | np447jx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5490 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328339 | 194487 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JY | NP447JY | np44 7jy | np447jy | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5521 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328306 | 194484 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7JZ | NP447JZ | np44 7jz | np447jz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5531 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328280 | 194401 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LA | NP447LA | np44 7la | np447la | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5609 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328202 | 194408 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LB | NP447LB | np44 7lb | np447lb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5673 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328143 | 194437 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LD | NP447LD | np44 7ld | np447ld | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5212 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328558 | 194119 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LE | NP447LE | np44 7le | np447le | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5571 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328225 | 194317 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LF | NP447LF | np44 7lf | np447lf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5372 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328411 | 194220 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LG | NP447LG | np44 7lg | np447lg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5594 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328130 | 193547 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LH | NP447LH | np44 7lh | np447lh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5605 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 328117 | 193461 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LJ | NP447LJ | np44 7lj | np447lj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5732 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 327990 | 193479 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LL | NP447LL | np44 7ll | np447ll | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5733 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327991 | 193562 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LN | NP447LN | np44 7ln | np447ln | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5836 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327888 | 193551 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LP | NP447LP | np44 7lp | np447lp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5847 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 327876 | 193492 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LQ | NP447LQ | np44 7lq | np447lq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6099 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327624 | 193533 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LR | NP447LR | np44 7lr | np447lr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5946 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 327779 | 193606 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LS | NP447LS | np44 7ls | np447ls | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 6550 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 327172 | 193395 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LT | NP447LT | np44 7lt | np447lt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5696 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328086 | 194232 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7LU | NP447LU | np44 7lu | np447lu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4903 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328881 | 194190 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7NE | NP447NE | np44 7ne | np447ne | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5143 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328691 | 194478 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7NF | NP447NF | np44 7nf | np447nf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5285 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 328552 | 194505 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7NX | NP447NX | np44 7nx | np447nx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4845 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328920 | 194054 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7NY | NP447NY | np44 7ny | np447ny | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4812 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328943 | 193976 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7NZ | NP447NZ | np44 7nz | np447nz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4954 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328805 | 194013 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7PA | NP447PA | np44 7pa | np447pa | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5018 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328797 | 194372 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7PB | NP447PB | np44 7pb | np447pb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4907 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328901 | 194327 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7PD | NP447PD | np44 7pd | np447pd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4699 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329134 | 194425 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7PE | NP447PE | np44 7pe | np447pe | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4862 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328959 | 194389 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7PF | NP447PF | np44 7pf | np447pf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5151 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328575 | 193625 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7PG | NP447PG | np44 7pg | np447pg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4520 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329294 | 194319 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7PH | NP447PH | np44 7ph | np447ph | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5142 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328598 | 193837 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7PJ | NP447PJ | np44 7pj | np447pj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5149 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328597 | 193914 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7PL | NP447PL | np44 7pl | np447pl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5000 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328736 | 193789 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7PN | NP447PN | np44 7pn | np447pn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5004 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 328726 | 193699 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7US | NP447US | np44 7us | np447us | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5348 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328383 | 193726 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7UT | NP447UT | np44 7ut | np447ut | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5271 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328461 | 193742 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7UU | NP447UU | np44 7uu | np447uu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 5292 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 328455 | 193928 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7XA | NP447XA | np44 7xa | np447xa | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4514 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329273 | 194175 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 7XB | NP447XB | np44 7xb | np447xb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4423 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 329353 | 194104 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8AD | NP448AD | np44 8ad | np448ad | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1938 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 331853 | 193927 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8AE | NP448AE | np44 8ae | np448ae | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2096 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 331629 | 193548 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8AF | NP448AF | np44 8af | np448af | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2076 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 331647 | 193502 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8DG | NP448DG | np44 8dg | np448dg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2044 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 331688 | 193627 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8DQ | NP448DQ | np44 8dq | np448dq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 1948 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 331781 | 193586 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8HN | NP448HN | np44 8hn | np448hn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3478 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330533 | 195086 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8HP | NP448HP | np44 8hp | np448hp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3623 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330346 | 194726 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8HQ | NP448HQ | np44 8hq | np448hq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 4048 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 329871 | 194659 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8HR | NP448HR | np44 8hr | np448hr | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3513 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330413 | 194593 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8HS | NP448HS | np44 8hs | np448hs | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3525 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330414 | 194630 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8HT | NP448HT | np44 8ht | np448ht | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3596 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330323 | 194586 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8HU | NP448HU | np44 8hu | np448hu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3453 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330461 | 194548 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8HW | NP448HW | np44 8hw | np448hw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3598 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330434 | 194872 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8HX | NP448HX | np44 8hx | np448hx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3440 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330498 | 194611 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8HY | NP448HY | np44 8hy | np448hy | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3247 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330619 | 194368 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8HZ | NP448HZ | np44 8hz | np448hz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3244 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330584 | 194234 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8JA | NP448JA | np44 8ja | np448ja | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3373 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330536 | 194520 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8JB | NP448JB | np44 8jb | np448jb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3275 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330622 | 194469 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8JD | NP448JD | np44 8jd | np448jd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3213 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330677 | 194438 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8JE | NP448JE | np44 8je | np448je | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3134 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330662 | 194090 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8JF | NP448JF | np44 8jf | np448jf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3179 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330634 | 194170 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8JG | NP448JG | np44 8jg | np448jg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3293 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330535 | 194241 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8JH | NP448JH | np44 8jh | np448jh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3368 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 330495 | 194378 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8JJ | NP448JJ | np44 8jj | np448jj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3384 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330505 | 194462 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8JL | NP448JL | np44 8jl | np448jl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3446 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330460 | 194522 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8JN | NP448JN | np44 8jn | np448jn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3354 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330580 | 194585 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8JQ | NP448JQ | np44 8jq | np448jq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3335 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330519 | 194340 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RA | NP448RA | np44 8ra | np448ra | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3321 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330681 | 195275 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RB | NP448RB | np44 8rb | np448rb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3301 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330702 | 195229 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RD | NP448RD | np44 8rd | np448rd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3553 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330410 | 194699 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RE | NP448RE | np44 8re | np448re | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3373 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330638 | 195089 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RF | NP448RF | np44 8rf | np448rf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3382 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330653 | 194870 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RG | NP448RG | np44 8rg | np448rg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3317 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330692 | 195120 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RH | NP448RH | np44 8rh | np448rh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3463 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330524 | 194741 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RJ | NP448RJ | np44 8rj | np448rj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3428 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330588 | 195032 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RL | NP448RL | np44 8rl | np448rl | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3416 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330594 | 195109 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RN | NP448RN | np44 8rn | np448rn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3479 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330541 | 194989 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RP | NP448RP | np44 8rp | np448rp | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3479 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330549 | 194839 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RQ | NP448RQ | np44 8rq | np448rq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3312 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330702 | 195064 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RR | NP448RR | np44 8rr | np448rr | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3514 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330508 | 194967 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RS | NP448RS | np44 8rs | np448rs | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3541 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330488 | 194910 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RT | NP448RT | np44 8rt | np448rt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3407 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330610 | 195021 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RU | NP448RU | np44 8ru | np448ru | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3317 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330710 | 194939 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RW | NP448RW | np44 8rw | np448rw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3438 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330588 | 194940 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RX | NP448RX | np44 8rx | np448rx | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3349 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330689 | 194857 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RY | NP448RY | np44 8ry | np448ry | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3434 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330597 | 194896 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8RZ | NP448RZ | np44 8rz | np448rz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3429 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330608 | 194847 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SA | NP448SA | np44 8sa | np448sa | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3382 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330605 | 194724 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SB | NP448SB | np44 8sb | np448sb | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3406 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330572 | 194708 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SD | NP448SD | np44 8sd | np448sd | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3437 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330535 | 194698 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SE | NP448SE | np44 8se | np448se | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3355 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330680 | 194826 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SF | NP448SF | np44 8sf | np448sf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3344 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330657 | 194749 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SG | NP448SG | np44 8sg | np448sg | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3449 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330510 | 194669 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SH | NP448SH | np44 8sh | np448sh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3409 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330540 | 194636 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SJ | NP448SJ | np44 8sj | np448sj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3483 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330470 | 194658 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SL | NP448SL | np44 8sl | np448sl | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3568 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330426 | 194777 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SN | NP448SN | np44 8sn | np448sn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3290 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330668 | 194636 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SR | NP448SR | np44 8sr | np448sr | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3424 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330578 | 195280 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SS | NP448SS | np44 8ss | np448ss | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3517 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330487 | 195216 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8ST | NP448ST | np44 8st | np448st | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3786 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330224 | 195098 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SU | NP448SU | np44 8su | np448su | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3818 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330201 | 194889 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SX | NP448SX | np44 8sx | np448sx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3677 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330322 | 194812 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SY | NP448SY | np44 8sy | np448sy | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3798 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330216 | 195041 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8SZ | NP448SZ | np44 8sz | np448sz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3861 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330152 | 195049 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TA | NP448TA | np44 8ta | np448ta | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3542 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330464 | 195166 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TB | NP448TB | np44 8tb | np448tb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3649 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330356 | 195191 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TD | NP448TD | np44 8td | np448td | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3574 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330438 | 195076 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TE | NP448TE | np44 8te | np448te | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3674 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330329 | 195226 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TF | NP448TF | np44 8tf | np448tf | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3753 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330252 | 195185 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TG | NP448TG | np44 8tg | np448tg | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3634 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330375 | 195113 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TH | NP448TH | np44 8th | np448th | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3660 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330354 | 195039 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TJ | NP448TJ | np44 8tj | np448tj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3668 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330341 | 195114 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TL | NP448TL | np44 8tl | np448tl | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3753 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330259 | 195068 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TN | NP448TN | np44 8tn | np448tn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3835 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330187 | 194950 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TP | NP448TP | np44 8tp | np448tp | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3805 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330201 | 195156 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TQ | NP448TQ | np44 8tq | np448tq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3720 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 330294 | 195039 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TS | NP448TS | np44 8ts | np448ts | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3165 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330860 | 194961 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TT | NP448TT | np44 8tt | np448tt | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3228 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330809 | 194803 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TU | NP448TU | np44 8tu | np448tu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3168 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330836 | 194719 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TX | NP448TX | np44 8tx | np448tx | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2856 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 331012 | 194315 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TY | NP448TY | np44 8ty | np448ty | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2983 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330908 | 194401 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8TZ | NP448TZ | np44 8tz | np448tz | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2839 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330987 | 194174 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UA | NP448UA | np44 8ua | np448ua | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2830 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330983 | 194126 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UB | NP448UB | np44 8ub | np448ub | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2781 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330988 | 193923 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UD | NP448UD | np44 8ud | np448ud | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2796 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330951 | 193794 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UE | NP448UE | np44 8ue | np448ue | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2892 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330912 | 194097 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UF | NP448UF | np44 8uf | np448uf | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2885 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330878 | 193902 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UG | NP448UG | np44 8ug | np448ug | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3102 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330854 | 194593 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UH | NP448UH | np44 8uh | np448uh | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2999 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330870 | 194341 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UJ | NP448UJ | np44 8uj | np448uj | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2953 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330892 | 194255 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UL | NP448UL | np44 8ul | np448ul | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2987 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330857 | 194257 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UN | NP448UN | np44 8un | np448un | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3051 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330852 | 194449 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UP | NP448UP | np44 8up | np448up | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2778 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330979 | 193855 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UQ | NP448UQ | np44 8uq | np448uq | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3118 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330776 | 194434 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UR | NP448UR | np44 8ur | np448ur | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3015 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330819 | 194228 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8US | NP448US | np44 8us | np448us | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3191 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330783 | 194654 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UT | NP448UT | np44 8ut | np448ut | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3160 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330815 | 194651 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UU | NP448UU | np44 8uu | np448uu | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3078 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330834 | 194476 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8UW | NP448UW | np44 8uw | np448uw | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 3043 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 330844 | 194401 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 8YN | NP448YN | np44 8yn | np448yn | Torfaen | Tor-Faen | STW Serving Court Farm Wtw | 2840 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 331159 | 194636 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9BY | NP449BY | np44 9by | np449by | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9BZ | NP449BZ | np44 9bz | np449bz | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9DA | NP449DA | np44 9da | np449da | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9DD | NP449DD | np44 9dd | np449dd | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9DH | NP449DH | np44 9dh | np449dh | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9DJ | NP449DJ | np44 9dj | np449dj | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9DN | NP449DN | np44 9dn | np449dn | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9DQ | NP449DQ | np44 9dq | np449dq | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9DS | NP449DS | np44 9ds | np449ds | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9DT | NP449DT | np44 9dt | np449dt | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9DW | NP449DW | np44 9dw | np449dw | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9EA | NP449EA | np44 9ea | np449ea | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9EB | NP449EB | np44 9eb | np449eb | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9ED | NP449ED | np44 9ed | np449ed | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 4655 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 329352 | 195565 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP44 9SA | NP449SA | np44 9sa | np449sa | Torfaen | Tor-Faen | Llandegfedd (Waunypwll) STW | 3207 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 330796 | 195459 | Torfaen LPA | SO | River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council
NP7 0AA | NP70AA | np7 0aa | np70aa | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1000 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325348 | 214714 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AB | NP70AB | np7 0ab | np70ab | Monmouthshire | Sir Fynwy | Aberbaiden STW | 988 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325364 | 214672 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AD | NP70AD | np7 0ad | np70ad | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1416 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324940 | 214615 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AE | NP70AE | np7 0ae | np70ae | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1111 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325248 | 214610 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AF | NP70AF | np7 0af | np70af | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1527 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324838 | 214540 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AG | NP70AG | np7 0ag | np70ag | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1243 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325115 | 214608 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AH | NP70AH | np7 0ah | np70ah | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1312 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325054 | 214553 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AJ | NP70AJ | np7 0aj | np70aj | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1482 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324875 | 214606 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AL | NP70AL | np7 0al | np70al | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1415 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324932 | 214733 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AN | NP70AN | np7 0an | np70an | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1298 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325049 | 214733 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AP | NP70AP | np7 0ap | np70ap | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1535 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324818 | 214634 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AQ | NP70AQ | np7 0aq | np70aq | Monmouthshire | Sir Fynwy | Brynmawr STW | 1293 | 1434 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.73 | 14.25 | 15.76 | 322094 | 212504 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AR | NP70AR | np7 0ar | np70ar | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1621 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324733 | 214626 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AS | NP70AS | np7 0as | np70as | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1690 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324639 | 214599 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AT | NP70AT | np7 0at | np70at | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1661 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324698 | 214576 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AU | NP70AU | np7 0au | np70au | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1629 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324727 | 214604 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AW | NP70AW | np7 0aw | np70aw | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1200 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325150 | 214679 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AX | NP70AX | np7 0ax | np70ax | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1217 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324784 | 215194 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AY | NP70AY | np7 0ay | np70ay | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1188 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324776 | 215224 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0AZ | NP70AZ | np7 0az | np70az | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1072 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 325516 | 215456 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BA | NP70BA | np7 0ba | np70ba | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1111 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324746 | 215296 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BB | NP70BB | np7 0bb | np70bb | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1020 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324709 | 215382 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BD | NP70BD | np7 0bd | np70bd | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1199 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324864 | 215277 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BE | NP70BE | np7 0be | np70be | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1124 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324853 | 215366 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BG | NP70BG | np7 0bg | np70bg | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1152 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324916 | 215387 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BH | NP70BH | np7 0bh | np70bh | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1067 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324836 | 215428 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BJ | NP70BJ | np7 0bj | np70bj | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1313 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325038 | 214886 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BL | NP70BL | np7 0bl | np70bl | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1285 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325062 | 214801 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BN | NP70BN | np7 0bn | np70bn | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1582 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324765 | 214754 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BP | NP70BP | np7 0bp | np70bp | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1492 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324856 | 214843 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BR | NP70BR | np7 0br | np70br | Monmouthshire | Sir Fynwy | Brynmawr STW | 2325 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 323009 | 213146 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BS | NP70BS | np7 0bs | np70bs | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1487 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324767 | 214871 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BT | NP70BT | np7 0bt | np70bt | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1536 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324720 | 214795 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BW | NP70BW | np7 0bw | np70bw | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1488 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324860 | 214717 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BX | NP70BX | np7 0bx | np70bx | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1447 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324519 | 214815 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0BY | NP70BY | np7 0by | np70by | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1915 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 324402 | 214310 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DA | NP70DA | np7 0da | np70da | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1665 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324617 | 214618 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DB | NP70DB | np7 0db | np70db | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1599 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324545 | 214665 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DD | NP70DD | np7 0dd | np70dd | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1613 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324518 | 214643 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DE | NP70DE | np7 0de | np70de | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1620 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324730 | 214680 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DF | NP70DF | np7 0df | np70df | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1491 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324573 | 214787 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DG | NP70DG | np7 0dg | np70dg | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1359 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324514 | 214906 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DL | NP70DL | np7 0dl | np70dl | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1299 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324503 | 214966 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DN | NP70DN | np7 0dn | np70dn | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1254 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 324340 | 214970 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DP | NP70DP | np7 0dp | np70dp | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1533 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324643 | 214767 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DQ | NP70DQ | np7 0dq | np70dq | Monmouthshire | Sir Fynwy | Glangrwyney STW | 2208 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 323445 | 214092 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DR | NP70DR | np7 0dr | np70dr | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1437 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324702 | 214896 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DS | NP70DS | np7 0ds | np70ds | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1356 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324831 | 215058 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DT | NP70DT | np7 0dt | np70dt | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1452 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324793 | 214925 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DU | NP70DU | np7 0du | np70du | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1558 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324789 | 214725 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DW | NP70DW | np7 0dw | np70dw | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1365 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 324422 | 214874 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DX | NP70DX | np7 0dx | np70dx | Monmouthshire | Sir Fynwy | Aberbaiden STW | 968 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325398 | 214586 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DY | NP70DY | np7 0dy | np70dy | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1647 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 324417 | 214584 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0DZ | NP70DZ | np7 0dz | np70dz | Monmouthshire | Sir Fynwy | Glangrwyney STW | 2112 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 323511 | 214173 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EA | NP70EA | np7 0ea | np70ea | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1015 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324643 | 215343 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EB | NP70EB | np7 0eb | np70eb | Monmouthshire | Sir Fynwy | Aberbaiden STW | 896 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325498 | 215065 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0ED | NP70ED | np7 0ed | np70ed | Monmouthshire | Sir Fynwy | Aberbaiden STW | 864 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325482 | 214769 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EE | NP70EE | np7 0ee | np70ee | Monmouthshire | Sir Fynwy | Glangrwyney STW | 916 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 324757 | 215562 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EF | NP70EF | np7 0ef | np70ef | Monmouthshire | Sir Fynwy | Aberbaiden STW | 635 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 325793 | 214467 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EG | NP70EG | np7 0eg | np70eg | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1061 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 324540 | 215235 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EH | NP70EH | np7 0eh | np70eh | Monmouthshire | Sir Fynwy | Glangrwyney STW | 920 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 323896 | 215303 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EJ | NP70EJ | np7 0ej | np70ej | Monmouthshire | Sir Fynwy | Aberbaiden STW | 919 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325428 | 214746 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EL | NP70EL | np7 0el | np70el | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1551 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 324253 | 214657 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EN | NP70EN | np7 0en | np70en | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1688 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 324167 | 214514 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EP | NP70EP | np7 0ep | np70ep | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1753 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 324304 | 214459 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EQ | NP70EQ | np7 0eq | np70eq | Monmouthshire | Sir Fynwy | Aberbaiden STW | 999 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 325505 | 215317 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0ER | NP70ER | np7 0er | np70er | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1982 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 323818 | 214239 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0ES | NP70ES | np7 0es | np70es | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1936 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 323833 | 214283 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0ET | NP70ET | np7 0et | np70et | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1997 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 323769 | 214231 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EU | NP70EU | np7 0eu | np70eu | Monmouthshire | Sir Fynwy | Glangrwyney STW | 2026 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 323727 | 214209 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EW | NP70EW | np7 0ew | np70ew | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1585 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 323962 | 214622 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EX | NP70EX | np7 0ex | np70ex | Monmouthshire | Sir Fynwy | Glangrwyney STW | 854 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 324639 | 215538 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EY | NP70EY | np7 0ey | np70ey | Monmouthshire | Sir Fynwy | Glangrwyney STW | 2132 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 323530 | 214146 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0EZ | NP70EZ | np7 0ez | np70ez | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1100 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325248 | 214834 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0FA | NP70FA | np7 0fa | np70fa | Monmouthshire | Sir Fynwy | Aberbaiden STW | 987 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 325359 | 214769 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HA | NP70HA | np7 0ha | np70ha | Monmouthshire | Sir Fynwy | Glangrwyney STW | 2334 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 323506 | 213944 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HD | NP70HD | np7 0hd | np70hd | Monmouthshire | Sir Fynwy | Glangrwyney STW | 2533 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 323267 | 213809 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HF | NP70HF | np7 0hf | np70hf | Monmouthshire | Sir Fynwy | Glangrwyney STW | 2336 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 323125 | 214078 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HG | NP70HG | np7 0hg | np70hg | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1498 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 323169 | 215027 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HH | NP70HH | np7 0hh | np70hh | Monmouthshire | Sir Fynwy | Brynmawr STW | 2186 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 322072 | 214189 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HL | NP70HL | np7 0hl | np70hl | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1721 | 1266 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.6 | 12.58 | 13.91 | 324927 | 213806 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HN | NP70HN | np7 0hn | np70hn | Monmouthshire | Sir Fynwy | Glangrwyney STW | 2275 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 324141 | 213926 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HP | NP70HP | np7 0hp | np70hp | Monmouthshire | Sir Fynwy | Aberbaiden STW | 2382 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 324223 | 213700 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HR | NP70HR | np7 0hr | np70hr | Monmouthshire | Sir Fynwy | Glangrwyney STW | 2638 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 323563 | 213618 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HS | NP70HS | np7 0hs | np70hs | Monmouthshire | Sir Fynwy | Aberbaiden STW | 2527 | 1341 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.99 | 13.33 | 14.73 | 324303 | 213292 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HT | NP70HT | np7 0ht | np70ht | Monmouthshire | Sir Fynwy | Brynmawr STW | 2515 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 322964 | 213697 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HU | NP70HU | np7 0hu | np70hu | Monmouthshire | Sir Fynwy | Brynmawr STW | 1701 | 1434 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.73 | 14.25 | 15.76 | 322443 | 212867 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HW | NP70HW | np7 0hw | np70hw | Monmouthshire | Sir Fynwy | Glangrwyney STW | 2047 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 324256 | 214160 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0HY | NP70HY | np7 0hy | np70hy | Monmouthshire | Sir Fynwy | Brynmawr STW | 1732 | 1434 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.73 | 14.25 | 15.76 | 322463 | 212909 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LA | NP70LA | np7 0la | np70la | Monmouthshire | Sir Fynwy | Brynmawr STW | 1732 | 1434 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.73 | 14.25 | 15.76 | 322468 | 212891 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LB | NP70LB | np7 0lb | np70lb | Monmouthshire | Sir Fynwy | Brynmawr STW | 1964 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 322626 | 213142 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LE | NP70LE | np7 0le | np70le | Monmouthshire | Sir Fynwy | Brynmawr STW | 1349 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322152 | 212341 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LF | NP70LF | np7 0lf | np70lf | Monmouthshire | Sir Fynwy | Brynmawr STW | 2414 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 322939 | 213535 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LG | NP70LG | np7 0lg | np70lg | Monmouthshire | Sir Fynwy | Brynmawr STW | 2027 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 322686 | 213162 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LH | NP70LH | np7 0lh | np70lh | Monmouthshire | Sir Fynwy | Brynmawr STW | 2180 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 322783 | 213324 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LJ | NP70LJ | np7 0lj | np70lj | Monmouthshire | Sir Fynwy | Brynmawr STW | 2068 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 322813 | 212900 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LL | NP70LL | np7 0ll | np70ll | Monmouthshire | Sir Fynwy | Brynmawr STW | 1703 | 1434 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.73 | 14.25 | 15.76 | 322439 | 212886 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LN | NP70LN | np7 0ln | np70ln | Monmouthshire | Sir Fynwy | Brynmawr STW | 1611 | 1434 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.73 | 14.25 | 15.76 | 322359 | 212831 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LP | NP70LP | np7 0lp | np70lp | Monmouthshire | Sir Fynwy | Brynmawr STW | 2252 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 323005 | 212885 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LR | NP70LR | np7 0lr | np70lr | Monmouthshire | Sir Fynwy | Brynmawr STW | 2292 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 322996 | 213079 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LS | NP70LS | np7 0ls | np70ls | Monmouthshire | Sir Fynwy | Brynmawr STW | 1972 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 322722 | 212867 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LT | NP70LT | np7 0lt | np70lt | Monmouthshire | Sir Fynwy | Brynmawr STW | 1932 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 322669 | 212916 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LW | NP70LW | np7 0lw | np70lw | Monmouthshire | Sir Fynwy | Brynmawr STW | 727 | 1434 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.73 | 14.25 | 15.76 | 321508 | 212592 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LY | NP70LY | np7 0ly | np70ly | Monmouthshire | Sir Fynwy | Brynmawr STW | 2352 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 323056 | 213089 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0LZ | NP70LZ | np7 0lz | np70lz | Monmouthshire | Sir Fynwy | Brynmawr STW | 2183 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 322908 | 212991 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NA | NP70NA | np7 0na | np70na | Monmouthshire | Sir Fynwy | Brynmawr STW | 2278 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 323013 | 212967 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NB | NP70NB | np7 0nb | np70nb | Monmouthshire | Sir Fynwy | Brynmawr STW | 2306 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 323036 | 212988 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0ND | NP70ND | np7 0nd | np70nd | Monmouthshire | Sir Fynwy | Brynmawr STW | 2354 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 323079 | 213014 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NE | NP70NE | np7 0ne | np70ne | Monmouthshire | Sir Fynwy | Brynmawr STW | 2182 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 322928 | 212911 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NF | NP70NF | np7 0nf | np70nf | Monmouthshire | Sir Fynwy | Brynmawr STW | 2329 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 323046 | 213041 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NG | NP70NG | np7 0ng | np70ng | Monmouthshire | Sir Fynwy | Brynmawr STW | 2563 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 323194 | 213334 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NH | NP70NH | np7 0nh | np70nh | Monmouthshire | Sir Fynwy | Brynmawr STW | 1766 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 322553 | 212655 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NL | NP70NL | np7 0nl | np70nl | Monmouthshire | Sir Fynwy | Brynmawr STW | 1301 | 1434 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.73 | 14.25 | 15.76 | 322102 | 212502 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NN | NP70NN | np7 0nn | np70nn | Monmouthshire | Sir Fynwy | Brynmawr STW | 825 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 321614 | 212251 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NP | NP70NP | np7 0np | np70np | Monmouthshire | Sir Fynwy | Brynmawr STW | 658 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 321384 | 212096 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NR | NP70NR | np7 0nr | np70nr | Monmouthshire | Sir Fynwy | Brynmawr STW | 1150 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 321950 | 212306 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NS | NP70NS | np7 0ns | np70ns | Monmouthshire | Sir Fynwy | Brynmawr STW | 1358 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322162 | 212371 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NT | NP70NT | np7 0nt | np70nt | Monmouthshire | Sir Fynwy | Brynmawr STW | 1592 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322395 | 212335 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NU | NP70NU | np7 0nu | np70nu | Monmouthshire | Sir Fynwy | Brynmawr STW | 1146 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 321841 | 211920 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NW | NP70NW | np7 0nw | np70nw | Monmouthshire | Sir Fynwy | Brynmawr STW | 857 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 321602 | 212094 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0NY | NP70NY | np7 0ny | np70ny | Monmouthshire | Sir Fynwy | Brynmawr STW | 940 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 321580 | 211878 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PA | NP70PA | np7 0pa | np70pa | Monmouthshire | Sir Fynwy | Brynmawr STW | 886 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 321456 | 211808 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PB | NP70PB | np7 0pb | np70pb | Monmouthshire | Sir Fynwy | Brynmawr STW | 1415 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322018 | 211681 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PD | NP70PD | np7 0pd | np70pd | Monmouthshire | Sir Fynwy | Brynmawr STW | 1339 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322085 | 212019 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PF | NP70PF | np7 0pf | np70pf | Monmouthshire | Sir Fynwy | Brynmawr STW | 1374 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322087 | 211917 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PG | NP70PG | np7 0pg | np70pg | Monmouthshire | Sir Fynwy | Brynmawr STW | 1522 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322273 | 212010 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PH | NP70PH | np7 0ph | np70ph | Monmouthshire | Sir Fynwy | Brynmawr STW | 1803 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 322603 | 212282 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PL | NP70PL | np7 0pl | np70pl | Monmouthshire | Sir Fynwy | Brynmawr STW | 1740 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 322538 | 212260 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PN | NP70PN | np7 0pn | np70pn | Monmouthshire | Sir Fynwy | Brynmawr STW | 1865 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 322666 | 212294 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PP | NP70PP | np7 0pp | np70pp | Monmouthshire | Sir Fynwy | Brynmawr STW | 1697 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322446 | 211978 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PR | NP70PR | np7 0pr | np70pr | Monmouthshire | Sir Fynwy | Brynmawr STW | 1634 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322376 | 211960 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PS | NP70PS | np7 0ps | np70ps | Monmouthshire | Sir Fynwy | Brynmawr STW | 1759 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 322535 | 212095 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PT | NP70PT | np7 0pt | np70pt | Monmouthshire | Sir Fynwy | Brynmawr STW | 1810 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 322610 | 212276 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PU | NP70PU | np7 0pu | np70pu | Monmouthshire | Sir Fynwy | Brynmawr STW | 1609 | 1490 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.77 | 14.81 | 16.37 | 321852 | 211188 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PW | NP70PW | np7 0pw | np70pw | Monmouthshire | Sir Fynwy | Brynmawr STW | 1446 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322234 | 212193 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PY | NP70PY | np7 0py | np70py | Monmouthshire | Sir Fynwy | Brynmawr STW | 1632 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322429 | 212251 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0PZ | NP70PZ | np7 0pz | np70pz | Monmouthshire | Sir Fynwy | Brynmawr STW | 1513 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322300 | 212179 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0RA | NP70RA | np7 0ra | np70ra | Monmouthshire | Sir Fynwy | Brynmawr STW | 1788 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 322572 | 212139 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0RB | NP70RB | np7 0rb | np70rb | Monmouthshire | Sir Fynwy | Brynmawr STW | 2282 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 323062 | 212739 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0RD | NP70RD | np7 0rd | np70rd | Monmouthshire | Sir Fynwy | Brynmawr STW | 2519 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 323246 | 213027 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0RE | NP70RE | np7 0re | np70re | Monmouthshire | Sir Fynwy | Brynmawr STW | 1216 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322021 | 212398 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0RF | NP70RF | np7 0rf | np70rf | Monmouthshire | Sir Fynwy | Brynmawr STW | 304 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 320909 | 212123 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0RG | NP70RG | np7 0rg | np70rg | Monmouthshire | Sir Fynwy | Brynmawr STW | 214 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 320912 | 212224 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0RH | NP70RH | np7 0rh | np70rh | Monmouthshire | Sir Fynwy | Brynmawr STW | 1493 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 322241 | 212002 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0RL | NP70RL | np7 0rl | np70rl | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1500 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 324349 | 214721 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0RN | NP70RN | np7 0rn | np70rn | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1375 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 324268 | 214836 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0RP | NP70RP | np7 0rp | np70rp | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1414 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 324393 | 214817 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0RR | NP70RR | np7 0rr | np70rr | Monmouthshire | Sir Fynwy | Brynmawr STW | 2128 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 322875 | 212900 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 0RW | NP70RW | np7 0rw | np70rw | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1480 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 324448 | 214762 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 1AU | NP71AU | np7 1au | np71au | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1AX | NP71AX | np7 1ax | np71ax | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1BU | NP71BU | np7 1bu | np71bu | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1BW | NP71BW | np7 1bw | np71bw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1DG | NP71DG | np7 1dg | np71dg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1DJ | NP71DJ | np7 1dj | np71dj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1DP | NP71DP | np7 1dp | np71dp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1DT | NP71DT | np7 1dt | np71dt | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1DU | NP71DU | np7 1du | np71du | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1DX | NP71DX | np7 1dx | np71dx | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1DZ | NP71DZ | np7 1dz | np71dz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1EA | NP71EA | np7 1ea | np71ea | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1EB | NP71EB | np7 1eb | np71eb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 1ED | NP71ED | np7 1ed | np71ed | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AA | NP75AA | np7 5aa | np75aa | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1053 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329807 | 214222 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AD | NP75AD | np7 5ad | np75ad | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1043 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329820 | 214215 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AE | NP75AE | np7 5ae | np75ae | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1130 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329845 | 214310 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AF | NP75AF | np7 5af | np75af | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1119 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329849 | 214300 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AG | NP75AG | np7 5ag | np75ag | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1199 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214376 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AH | NP75AH | np7 5ah | np75ah | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1279 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329784 | 214449 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AJ | NP75AJ | np7 5aj | np75aj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1229 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329860 | 214414 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AL | NP75AL | np7 5al | np75al | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1396 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329661 | 214537 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AN | NP75AN | np7 5an | np75an | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1338 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329698 | 214487 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AQ | NP75AQ | np7 5aq | np75aq | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1294 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329453 | 214583 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AR | NP75AR | np7 5ar | np75ar | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1215 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329790 | 214385 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AS | NP75AS | np7 5as | np75as | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1242 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329829 | 214422 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AT | NP75AT | np7 5at | np75at | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1200 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329798 | 214372 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AU | NP75AU | np7 5au | np75au | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1140 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329823 | 214316 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AX | NP75AX | np7 5ax | np75ax | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1117 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329807 | 214288 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AY | NP75AY | np7 5ay | np75ay | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1389 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329550 | 214584 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5AZ | NP75AZ | np7 5az | np75az | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BA | NP75BA | np7 5ba | np75ba | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1176 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329787 | 214344 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BB | NP75BB | np7 5bb | np75bb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1170 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329724 | 214319 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BD | NP75BD | np7 5bd | np75bd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1188 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329682 | 214324 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BE | NP75BE | np7 5be | np75be | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1139 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329680 | 214271 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BG | NP75BG | np7 5bg | np75bg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1167 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329638 | 214285 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BH | NP75BH | np7 5bh | np75bh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1119 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329635 | 214231 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BJ | NP75BJ | np7 5bj | np75bj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1252 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329716 | 214403 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BL | NP75BL | np7 5bl | np75bl | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1283 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329647 | 214413 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BN | NP75BN | np7 5bn | np75bn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1324 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329648 | 214456 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BP | NP75BP | np7 5bp | np75bp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1344 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329638 | 214474 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BQ | NP75BQ | np7 5bq | np75bq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1326 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329710 | 214478 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BS | NP75BS | np7 5bs | np75bs | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1319 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329579 | 214425 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BT | NP75BT | np7 5bt | np75bt | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1357 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329548 | 214453 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BU | NP75BU | np7 5bu | np75bu | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1374 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329510 | 214467 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BW | NP75BW | np7 5bw | np75bw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1270 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329586 | 214375 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BX | NP75BX | np7 5bx | np75bx | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1401 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329554 | 214540 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BY | NP75BY | np7 5by | np75by | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1303 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329444 | 214342 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5BZ | NP75BZ | np7 5bz | np75bz | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1398 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329555 | 214559 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DA | NP75DA | np7 5da | np75da | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1337 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329454 | 214407 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DB | NP75DB | np7 5db | np75db | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1207 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329409 | 214207 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DD | NP75DD | np7 5dd | np75dd | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1323 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329450 | 214442 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DE | NP75DE | np7 5de | np75de | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1258 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329424 | 214278 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DF | NP75DF | np7 5df | np75df | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1148 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329346 | 214087 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DG | NP75DG | np7 5dg | np75dg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1241 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329201 | 214080 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DH | NP75DH | np7 5dh | np75dh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1137 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329497 | 214180 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DJ | NP75DJ | np7 5dj | np75dj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1201 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329696 | 214343 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DL | NP75DL | np7 5dl | np75dl | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1096 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329574 | 214177 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DN | NP75DN | np7 5dn | np75dn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1180 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329474 | 214217 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DP | NP75DP | np7 5dp | np75dp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1213 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329503 | 214271 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DQ | NP75DQ | np7 5dq | np75dq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1246 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329511 | 214313 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DR | NP75DR | np7 5dr | np75dr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1297 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329466 | 214347 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DS | NP75DS | np7 5ds | np75ds | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1244 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329567 | 214338 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DT | NP75DT | np7 5dt | np75dt | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1265 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329445 | 214298 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DU | NP75DU | np7 5du | np75du | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1292 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329519 | 214368 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DW | NP75DW | np7 5dw | np75dw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1170 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329509 | 214226 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DX | NP75DX | np7 5dx | np75dx | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1057 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329652 | 214171 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DY | NP75DY | np7 5dy | np75dy | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1323 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329461 | 214483 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5DZ | NP75DZ | np7 5dz | np75dz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1193 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330498 | 214324 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5EA | NP75EA | np7 5ea | np75ea | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1164 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329579 | 214255 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5EE | NP75EE | np7 5ee | np75ee | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 859 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329911 | 214048 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5EF | NP75EF | np7 5ef | np75ef | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1093 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329589 | 214181 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5EG | NP75EG | np7 5eg | np75eg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1008 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329862 | 214189 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5EH | NP75EH | np7 5eh | np75eh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 956 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329930 | 214150 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5EN | NP75EN | np7 5en | np75en | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 909 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329943 | 214104 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5EQ | NP75EQ | np7 5eq | np75eq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 850 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329986 | 214050 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5ER | NP75ER | np7 5er | np75er | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 854 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330033 | 214058 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5ES | NP75ES | np7 5es | np75es | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1592 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329771 | 214776 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5EU | NP75EU | np7 5eu | np75eu | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 958 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329969 | 214157 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5EW | NP75EW | np7 5ew | np75ew | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 834 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330016 | 214037 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5EX | NP75EX | np7 5ex | np75ex | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 715 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330056 | 213920 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HB | NP75HB | np7 5hb | np75hb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 947 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329974 | 214146 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HD | NP75HD | np7 5hd | np75hd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1019 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329961 | 214217 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HE | NP75HE | np7 5he | np75he | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 639 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330058 | 213844 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HF | NP75HF | np7 5hf | np75hf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 851 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330177 | 214051 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HG | NP75HG | np7 5hg | np75hg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 699 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330281 | 213876 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HH | NP75HH | np7 5hh | np75hh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 567 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330252 | 213747 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HJ | NP75HJ | np7 5hj | np75hj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 526 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330163 | 213726 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HL | NP75HL | np7 5hl | np75hl | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 417 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330335 | 213537 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HN | NP75HN | np7 5hn | np75hn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 574 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330405 | 213680 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HP | NP75HP | np7 5hp | np75hp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 588 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330174 | 213787 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HQ | NP75HQ | np7 5hq | np75hq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 495 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330472 | 213511 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HR | NP75HR | np7 5hr | np75hr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 387 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330264 | 213547 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HS | NP75HS | np7 5hs | np75hs | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 514 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330445 | 213569 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HT | NP75HT | np7 5ht | np75ht | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 472 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330433 | 213521 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HW | NP75HW | np7 5hw | np75hw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 523 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330383 | 213634 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HX | NP75HX | np7 5hx | np75hx | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 542 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330470 | 213584 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HY | NP75HY | np7 5hy | np75hy | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 574 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 330534 | 213560 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5HZ | NP75HZ | np7 5hz | np75hz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 666 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 330506 | 213719 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JA | NP75JA | np7 5ja | np75ja | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 514 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 330501 | 213503 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JB | NP75JB | np7 5jb | np75jb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 542 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 330500 | 213550 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JD | NP75JD | np7 5jd | np75jd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1474 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330617 | 214579 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JP | NP75JP | np7 5jp | np75jp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 997 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 330538 | 214092 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JQ | NP75JQ | np7 5jq | np75jq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1064 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330130 | 214269 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JR | NP75JR | np7 5jr | np75jr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1054 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330147 | 214258 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JS | NP75JS | np7 5js | np75js | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1093 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330135 | 214297 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JT | NP75JT | np7 5jt | np75jt | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1318 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 330545 | 214440 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JU | NP75JU | np7 5ju | np75ju | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1585 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330697 | 214666 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JW | NP75JW | np7 5jw | np75jw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1413 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 330650 | 214499 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JX | NP75JX | np7 5jx | np75jx | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1401 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 330631 | 214494 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JY | NP75JY | np7 5jy | np75jy | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1264 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330445 | 214416 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5JZ | NP75JZ | np7 5jz | np75jz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1481 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330712 | 214546 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LA | NP75LA | np7 5la | np75la | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1082 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330427 | 214231 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LB | NP75LB | np7 5lb | np75lb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1208 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 330569 | 214311 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LD | NP75LD | np7 5ld | np75ld | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1035 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330121 | 214240 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LE | NP75LE | np7 5le | np75le | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 961 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330438 | 214098 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LF | NP75LF | np7 5lf | np75lf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 664 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330370 | 213804 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LG | NP75LG | np7 5lg | np75lg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 801 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 330527 | 213872 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LH | NP75LH | np7 5lh | np75lh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 728 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330379 | 213870 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LJ | NP75LJ | np7 5lj | np75lj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1162 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330298 | 214347 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LL | NP75LL | np7 5ll | np75ll | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 759 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330431 | 213880 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LN | NP75LN | np7 5ln | np75ln | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 909 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330402 | 214057 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LP | NP75LP | np7 5lp | np75lp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 752 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330305 | 213924 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LQ | NP75LQ | np7 5lq | np75lq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1136 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 330572 | 214231 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LR | NP75LR | np7 5lr | np75lr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 849 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330296 | 214027 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LT | NP75LT | np7 5lt | np75lt | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1158 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330233 | 214354 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LU | NP75LU | np7 5lu | np75lu | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 999 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330267 | 214187 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LW | NP75LW | np7 5lw | np75lw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 813 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330364 | 213968 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LX | NP75LX | np7 5lx | np75lx | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1184 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330457 | 214329 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LY | NP75LY | np7 5ly | np75ly | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1083 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330400 | 214241 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5LZ | NP75LZ | np7 5lz | np75lz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1203 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330392 | 214368 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5NA | NP75NA | np7 5na | np75na | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1030 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330154 | 214233 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5NB | NP75NB | np7 5nb | np75nb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1057 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330051 | 214262 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5ND | NP75ND | np7 5nd | np75nd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 925 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330038 | 214130 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5NE | NP75NE | np7 5ne | np75ne | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 875 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330068 | 214081 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5NF | NP75NF | np7 5nf | np75nf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 993 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330057 | 214198 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5NH | NP75NH | np7 5nh | np75nh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 975 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330030 | 214179 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5NJ | NP75NJ | np7 5nj | np75nj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 994 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330119 | 214199 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5NP | NP75NP | np7 5np | np75np | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 970 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330052 | 214175 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5NQ | NP75NQ | np7 5nq | np75nq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 953 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330168 | 214155 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5NT | NP75NT | np7 5nt | np75nt | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1105 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330007 | 214308 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5NW | NP75NW | np7 5nw | np75nw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1058 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330099 | 214264 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5PE | NP75PE | np7 5pe | np75pe | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1132 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329956 | 214331 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5PF | NP75PF | np7 5pf | np75pf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1298 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329881 | 214488 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5PH | NP75PH | np7 5ph | np75ph | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1145 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329879 | 214332 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5PJ | NP75PJ | np7 5pj | np75pj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1116 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330099 | 214321 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5PN | NP75PN | np7 5pn | np75pn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1109 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329928 | 214304 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5PP | NP75PP | np7 5pp | np75pp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1144 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330107 | 214349 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5PQ | NP75PQ | np7 5pq | np75pq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1306 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330261 | 214499 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5PR | NP75PR | np7 5pr | np75pr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1190 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330180 | 214392 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5PU | NP75PU | np7 5pu | np75pu | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1347 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330264 | 214540 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5PW | NP75PW | np7 5pw | np75pw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1407 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330231 | 214605 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5PY | NP75PY | np7 5py | np75py | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1410 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330298 | 214599 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RA | NP75RA | np7 5ra | np75ra | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1508 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330312 | 214696 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RB | NP75RB | np7 5rb | np75rb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1606 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330404 | 214779 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RD | NP75RD | np7 5rd | np75rd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1675 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330497 | 214828 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RE | NP75RE | np7 5re | np75re | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1653 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330598 | 214776 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RF | NP75RF | np7 5rf | np75rf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1556 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330638 | 214659 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RG | NP75RG | np7 5rg | np75rg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1603 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330465 | 214762 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RH | NP75RH | np7 5rh | np75rh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1578 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330561 | 214709 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RJ | NP75RJ | np7 5rj | np75rj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1315 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 330312 | 214500 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RL | NP75RL | np7 5rl | np75rl | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1478 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330444 | 214638 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RN | NP75RN | np7 5rn | np75rn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1549 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330509 | 214694 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RP | NP75RP | np7 5rp | np75rp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1521 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330449 | 214682 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RR | NP75RR | np7 5rr | np75rr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1457 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330398 | 214628 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RS | NP75RS | np7 5rs | np75rs | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1376 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330325 | 214560 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RT | NP75RT | np7 5rt | np75rt | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1011 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329860 | 214192 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RW | NP75RW | np7 5rw | np75rw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1621 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330541 | 214760 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5RY | NP75RY | np7 5ry | np75ry | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1084 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329863 | 214267 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SA | NP75SA | np7 5sa | np75sa | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1068 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329872 | 214253 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SD | NP75SD | np7 5sd | np75sd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1043 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329944 | 214239 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SE | NP75SE | np7 5se | np75se | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1198 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329943 | 214396 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SG | NP75SG | np7 5sg | np75sg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1446 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329927 | 214643 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SH | NP75SH | np7 5sh | np75sh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1563 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329912 | 214759 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SL | NP75SL | np7 5sl | np75sl | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1625 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330057 | 214830 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SN | NP75SN | np7 5sn | np75sn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1647 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330189 | 214849 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SP | NP75SP | np7 5sp | np75sp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1605 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330315 | 214793 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SR | NP75SR | np7 5sr | np75sr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1541 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330282 | 214733 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SS | NP75SS | np7 5ss | np75ss | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1525 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330216 | 214725 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SU | NP75SU | np7 5su | np75su | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1697 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330231 | 214896 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SW | NP75SW | np7 5sw | np75sw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1603 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330232 | 214801 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5SY | NP75SY | np7 5sy | np75sy | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1638 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329953 | 214838 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TA | NP75TA | np7 5ta | np75ta | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1685 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330028 | 214890 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TB | NP75TB | np7 5tb | np75tb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1686 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330149 | 214890 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TD | NP75TD | np7 5td | np75td | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1685 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330316 | 214874 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TE | NP75TE | np7 5te | np75te | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1681 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330380 | 214860 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TF | NP75TF | np7 5tf | np75tf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1642 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330348 | 214826 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TG | NP75TG | np7 5tg | np75tg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1682 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330421 | 214853 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TH | NP75TH | np7 5th | np75th | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1757 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330297 | 214949 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TL | NP75TL | np7 5tl | np75tl | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1738 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330012 | 214942 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TN | NP75TN | np7 5tn | np75tn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1609 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329844 | 214797 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TR | NP75TR | np7 5tr | np75tr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1291 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329948 | 214490 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TS | NP75TS | np7 5ts | np75ts | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1362 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329824 | 214543 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TT | NP75TT | np7 5tt | np75tt | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1355 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329837 | 214538 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5TU | NP75TU | np7 5tu | np75tu | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1396 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329786 | 214570 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UA | NP75UA | np7 5ua | np75ua | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1504 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329863 | 214693 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UB | NP75UB | np7 5ub | np75ub | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1424 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329827 | 214606 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UD | NP75UD | np7 5ud | np75ud | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1478 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329694 | 214632 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UF | NP75UF | np7 5uf | np75uf | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1275 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329421 | 214518 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UG | NP75UG | np7 5ug | np75ug | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1333 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329479 | 214514 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UH | NP75UH | np7 5uh | np75uh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1411 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329575 | 214522 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UL | NP75UL | np7 5ul | np75ul | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1188 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329205 | 214211 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UN | NP75UN | np7 5un | np75un | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1214 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329236 | 214211 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UP | NP75UP | np7 5up | np75up | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1236 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329215 | 214135 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UR | NP75UR | np7 5ur | np75ur | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1174 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329158 | 214161 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UU | NP75UU | np7 5uu | np75uu | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1162 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329247 | 214350 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UW | NP75UW | np7 5uw | np75uw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1226 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329326 | 214171 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UY | NP75UY | np7 5uy | np75uy | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1277 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329411 | 214473 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5UZ | NP75UZ | np7 5uz | np75uz | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1225 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329363 | 214495 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5WQ | NP75WQ | np7 5wq | np75wq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5YA | NP75YA | np7 5ya | np75ya | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1188 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329272 | 214342 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5YB | NP75YB | np7 5yb | np75yb | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1262 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329366 | 214381 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5YD | NP75YD | np7 5yd | np75yd | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1254 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329299 | 214246 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5YE | NP75YE | np7 5ye | np75ye | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1297 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329367 | 214288 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5YN | NP75YN | np7 5yn | np75yn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1051 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329857 | 214232 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5YT | NP75YT | np7 5yt | np75yt | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1479 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329752 | 214647 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 5ZT | NP75ZT | np7 5zt | np75zt | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AA | NP76AA | np7 6aa | np76aa | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1809 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330514 | 214962 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AB | NP76AB | np7 6ab | np76ab | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1879 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330550 | 215025 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AD | NP76AD | np7 6ad | np76ad | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1951 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330594 | 215088 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AE | NP76AE | np7 6ae | np76ae | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1847 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330657 | 214961 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AF | NP76AF | np7 6af | np76af | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1822 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330573 | 214960 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AG | NP76AG | np7 6ag | np76ag | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1796 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330643 | 214911 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AH | NP76AH | np7 6ah | np76ah | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1720 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330603 | 214845 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AJ | NP76AJ | np7 6aj | np76aj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1647 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330806 | 214685 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AL | NP76AL | np7 6al | np76al | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1879 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330467 | 215044 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AN | NP76AN | np7 6an | np76an | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1997 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330348 | 215185 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AP | NP76AP | np7 6ap | np76ap | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2291 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330263 | 215761 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AQ | NP76AQ | np7 6aq | np76aq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1636 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330752 | 214698 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AR | NP76AR | np7 6ar | np76ar | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2170 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330175 | 215663 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AS | NP76AS | np7 6as | np76as | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2240 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330267 | 215622 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AT | NP76AT | np7 6at | np76at | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2258 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330327 | 215507 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AU | NP76AU | np7 6au | np76au | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1760 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330880 | 214774 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AW | NP76AW | np7 6aw | np76aw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1841 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330407 | 215017 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AX | NP76AX | np7 6ax | np76ax | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2238 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330221 | 215727 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AY | NP76AY | np7 6ay | np76ay | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2209 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330384 | 215394 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6AZ | NP76AZ | np7 6az | np76az | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2258 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330221 | 215775 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BA | NP76BA | np7 6ba | np76ba | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2303 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330334 | 215623 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BB | NP76BB | np7 6bb | np76bb | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2306 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330323 | 215660 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BD | NP76BD | np7 6bd | np76bd | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2312 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330298 | 215734 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BE | NP76BE | np7 6be | np76be | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2298 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330363 | 215524 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BG | NP76BG | np7 6bg | np76bg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1920 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330214 | 215121 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BH | NP76BH | np7 6bh | np76bh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2015 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330213 | 215216 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BJ | NP76BJ | np7 6bj | np76bj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1887 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330673 | 214997 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BL | NP76BL | np7 6bl | np76bl | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2127 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330242 | 215329 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BN | NP76BN | np7 6bn | np76bn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2161 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330330 | 215352 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BP | NP76BP | np7 6bp | np76bp | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2062 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330110 | 215535 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BQ | NP76BQ | np7 6bq | np76bq | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2243 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330286 | 215580 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BR | NP76BR | np7 6br | np76br | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2084 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330825 | 215152 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BS | NP76BS | np7 6bs | np76bs | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2213 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330307 | 215419 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BT | NP76BT | np7 6bt | np76bt | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2036 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330157 | 215295 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BU | NP76BU | np7 6bu | np76bu | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1940 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330149 | 215144 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BW | NP76BW | np7 6bw | np76bw | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2070 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330180 | 215341 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6BY | NP76BY | np7 6by | np76by | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1947 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330295 | 215141 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DA | NP76DA | np7 6da | np76da | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1886 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330252 | 215084 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DB | NP76DB | np7 6db | np76db | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1956 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330019 | 215474 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DD | NP76DD | np7 6dd | np76dd | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1850 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329928 | 215415 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DE | NP76DE | np7 6de | np76de | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1869 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 329907 | 215524 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DF | NP76DF | np7 6df | np76df | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1868 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329969 | 215346 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DG | NP76DG | np7 6dg | np76dg | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1737 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329834 | 215340 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DH | NP76DH | np7 6dh | np76dh | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1689 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329770 | 215377 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DJ | NP76DJ | np7 6dj | np76dj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1818 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330189 | 215020 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DL | NP76DL | np7 6dl | np76dl | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2125 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330173 | 215546 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DN | NP76DN | np7 6dn | np76dn | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1701 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329773 | 215406 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DP | NP76DP | np7 6dp | np76dp | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1771 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329826 | 215463 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DR | NP76DR | np7 6dr | np76dr | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1742 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329783 | 215490 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DT | NP76DT | np7 6dt | np76dt | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1831 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 329852 | 215555 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DU | NP76DU | np7 6du | np76du | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1982 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330002 | 215588 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DW | NP76DW | np7 6dw | np76dw | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1952 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 329995 | 215526 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DX | NP76DX | np7 6dx | np76dx | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1986 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330046 | 215489 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6DY | NP76DY | np7 6dy | np76dy | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1924 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330064 | 215195 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EA | NP76EA | np7 6ea | np76ea | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1978 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330084 | 215343 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EB | NP76EB | np7 6eb | np76eb | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2092 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330181 | 215417 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6ED | NP76ED | np7 6ed | np76ed | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2182 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330256 | 215481 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EE | NP76EE | np7 6ee | np76ee | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1851 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330063 | 215056 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EF | NP76EF | np7 6ef | np76ef | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1894 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330123 | 215099 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EG | NP76EG | np7 6eg | np76eg | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1867 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330024 | 215099 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EH | NP76EH | np7 6eh | np76eh | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1636 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329799 | 215042 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EJ | NP76EJ | np7 6ej | np76ej | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1814 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330006 | 215018 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EL | NP76EL | np7 6el | np76el | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1722 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329890 | 215007 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EN | NP76EN | np7 6en | np76en | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1844 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329998 | 215115 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EP | NP76EP | np7 6ep | np76ep | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1837 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329957 | 215273 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EQ | NP76EQ | np7 6eq | np76eq | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1873 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330022 | 215148 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EU | NP76EU | np7 6eu | np76eu | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2090 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330541 | 215244 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EW | NP76EW | np7 6ew | np76ew | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1762 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329895 | 215210 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6EY | NP76EY | np7 6ey | np76ey | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2042 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330540 | 215195 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HA | NP76HA | np7 6ha | np76ha | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2178 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330547 | 215333 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HB | NP76HB | np7 6hb | np76hb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2303 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330581 | 215454 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HD | NP76HD | np7 6hd | np76hd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2396 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330688 | 215523 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HE | NP76HE | np7 6he | np76he | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2334 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330660 | 215466 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HF | NP76HF | np7 6hf | np76hf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2398 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330570 | 215553 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HG | NP76HG | np7 6hg | np76hg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2361 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330463 | 215535 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HJ | NP76HJ | np7 6hj | np76hj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2429 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330838 | 215514 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HL | NP76HL | np7 6hl | np76hl | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2315 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330500 | 215482 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HN | NP76HN | np7 6hn | np76hn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2232 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330481 | 215401 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HP | NP76HP | np7 6hp | np76hp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2171 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330465 | 215342 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HQ | NP76HQ | np7 6hq | np76hq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2714 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330907 | 215791 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HR | NP76HR | np7 6hr | np76hr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2067 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330461 | 215237 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HS | NP76HS | np7 6hs | np76hs | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2176 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330640 | 215308 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HT | NP76HT | np7 6ht | np76ht | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2473 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330760 | 215583 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HU | NP76HU | np7 6hu | np76hu | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2599 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330795 | 215704 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HW | NP76HW | np7 6hw | np76hw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2184 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330585 | 215331 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HX | NP76HX | np7 6hx | np76hx | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2441 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330693 | 215568 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HY | NP76HY | np7 6hy | np76hy | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2545 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330783 | 215652 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6HZ | NP76HZ | np7 6hz | np76hz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2130 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330496 | 215295 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6JA | NP76JA | np7 6ja | np76ja | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2006 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 330482 | 215171 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6JX | NP76JX | np7 6jx | np76jx | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2921 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330902 | 216008 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6JY | NP76JY | np7 6jy | np76jy | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2982 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330863 | 216109 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6JZ | NP76JZ | np7 6jz | np76jz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2974 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 331014 | 216029 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LA | NP76LA | np7 6la | np76la | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2649 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330819 | 215749 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LB | NP76LB | np7 6lb | np76lb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2699 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330817 | 215802 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LD | NP76LD | np7 6ld | np76ld | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2751 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330881 | 215837 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LE | NP76LE | np7 6le | np76le | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2808 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330920 | 215885 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LF | NP76LF | np7 6lf | np76lf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2800 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330968 | 215861 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LG | NP76LG | np7 6lg | np76lg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2748 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330975 | 215804 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LH | NP76LH | np7 6lh | np76lh | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2674 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330529 | 216085 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LJ | NP76LJ | np7 6lj | np76lj | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2726 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330624 | 216016 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LL | NP76LL | np7 6ll | np76ll | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2678 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330540 | 216073 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LN | NP76LN | np7 6ln | np76ln | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2660 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330511 | 216090 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LP | NP76LP | np7 6lp | np76lp | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2826 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330675 | 216135 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LQ | NP76LQ | np7 6lq | np76lq | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2803 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330683 | 216070 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LR | NP76LR | np7 6lr | np76lr | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2819 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330646 | 216173 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LS | NP76LS | np7 6ls | np76ls | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2877 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330697 | 216202 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LT | NP76LT | np7 6lt | np76lt | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2943 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330772 | 216202 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LU | NP76LU | np7 6lu | np76lu | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2913 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330770 | 216141 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LW | NP76LW | np7 6lw | np76lw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2841 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330847 | 215941 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LX | NP76LX | np7 6lx | np76lx | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2855 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330754 | 216042 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LY | NP76LY | np7 6ly | np76ly | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2864 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330695 | 216178 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6LZ | NP76LZ | np7 6lz | np76lz | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2761 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330614 | 216111 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NA | NP76NA | np7 6na | np76na | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2580 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330491 | 215954 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NB | NP76NB | np7 6nb | np76nb | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2666 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330543 | 216043 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6ND | NP76ND | np7 6nd | np76nd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2742 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330764 | 215861 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NE | NP76NE | np7 6ne | np76ne | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2684 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330629 | 215906 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NF | NP76NF | np7 6nf | np76nf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2722 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330728 | 215849 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NG | NP76NG | np7 6ng | np76ng | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2604 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330607 | 215756 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NH | NP76NH | np7 6nh | np76nh | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2674 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330654 | 215822 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NJ | NP76NJ | np7 6nj | np76nj | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2937 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330842 | 216049 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NL | NP76NL | np7 6nl | np76nl | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2653 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330629 | 215828 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NP | NP76NP | np7 6np | np76np | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1842 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330768 | 214915 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NQ | NP76NQ | np7 6nq | np76nq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1865 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330862 | 214899 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NR | NP76NR | np7 6nr | np76nr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2056 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330875 | 215102 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NS | NP76NS | np7 6ns | np76ns | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2323 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 331053 | 215316 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NT | NP76NT | np7 6nt | np76nt | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2998 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 331291 | 215948 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NU | NP76NU | np7 6nu | np76nu | Monmouthshire | Sir Fynwy | Llanwenarth STW | 3373 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 331092 | 216510 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 6NW | NP76NW | np7 6nw | np76nw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1975 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330799 | 215045 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6NY | NP76NY | np7 6ny | np76ny | Monmouthshire | Sir Fynwy | Llanwenarth STW | 3138 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330879 | 216409 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PA | NP76PA | np7 6pa | np76pa | Monmouthshire | Sir Fynwy | Llanwenarth STW | 3367 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 330925 | 216757 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 6PB | NP76PB | np7 6pb | np76pb | Monmouthshire | Sir Fynwy | Llanwenarth STW | 3416 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 330688 | 217127 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 6PD | NP76PD | np7 6pd | np76pd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2030 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330669 | 215149 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PE | NP76PE | np7 6pe | np76pe | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2016 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330753 | 215106 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PF | NP76PF | np7 6pf | np76pf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2260 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330791 | 215351 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PG | NP76PG | np7 6pg | np76pg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2237 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 330724 | 215348 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PH | NP76PH | np7 6ph | np76ph | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2396 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330405 | 215698 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PJ | NP76PJ | np7 6pj | np76pj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2799 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330803 | 215910 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PL | NP76PL | np7 6pl | np76pl | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2494 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330476 | 215781 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PN | NP76PN | np7 6pn | np76pn | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2459 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330485 | 215665 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PP | NP76PP | np7 6pp | np76pp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2418 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330632 | 215560 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PQ | NP76PQ | np7 6pq | np76pq | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2900 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330672 | 216291 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PR | NP76PR | np7 6pr | np76pr | Monmouthshire | Sir Fynwy | Llanwenarth STW | 3020 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330771 | 216359 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PS | NP76PS | np7 6ps | np76ps | Monmouthshire | Sir Fynwy | Llanwenarth STW | 3074 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330800 | 216416 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PT | NP76PT | np7 6pt | np76pt | Monmouthshire | Sir Fynwy | Llanwenarth STW | 3162 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 331002 | 216235 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PU | NP76PU | np7 6pu | np76pu | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2998 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330707 | 216422 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PW | NP76PW | np7 6pw | np76pw | Monmouthshire | Sir Fynwy | Llanwenarth STW | 3015 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330838 | 216232 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PX | NP76PX | np7 6px | np76px | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2988 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330792 | 216259 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6PY | NP76PY | np7 6py | np76py | Monmouthshire | Sir Fynwy | Llanwenarth STW | 3372 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 331028 | 216613 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 6PZ | NP76PZ | np7 6pz | np76pz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 3070 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 331000 | 216134 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 6QA | NP76QA | np7 6qa | np76qa | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2982 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 330745 | 216328 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AA | NP77AA | np7 7aa | np77aa | Monmouthshire | Sir Fynwy | Llanwenarth STW | 913 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329058 | 215059 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AB | NP77AB | np7 7ab | np77ab | Monmouthshire | Sir Fynwy | Llanwenarth STW | 760 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328911 | 215018 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AD | NP77AD | np7 7ad | np77ad | Monmouthshire | Sir Fynwy | Llanwenarth STW | 640 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328802 | 214958 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AE | NP77AE | np7 7ae | np77ae | Monmouthshire | Sir Fynwy | Llanwenarth STW | 664 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328844 | 214813 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AF | NP77AF | np7 7af | np77af | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1504 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329555 | 215418 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AG | NP77AG | np7 7ag | np77ag | Monmouthshire | Sir Fynwy | Llanwenarth STW | 784 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328959 | 214895 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AH | NP77AH | np7 7ah | np77ah | Monmouthshire | Sir Fynwy | Llanwenarth STW | 835 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329014 | 214854 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AJ | NP77AJ | np7 7aj | np77aj | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1421 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329453 | 215440 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AL | NP77AL | np7 7al | np77al | Monmouthshire | Sir Fynwy | Llanwenarth STW | 837 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329011 | 214713 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AN | NP77AN | np7 7an | np77an | Monmouthshire | Sir Fynwy | Llanwenarth STW | 629 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328807 | 214766 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AP | NP77AP | np7 7ap | np77ap | Monmouthshire | Sir Fynwy | Llanwenarth STW | 895 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329069 | 214712 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AQ | NP77AQ | np7 7aq | np77aq | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1508 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329546 | 215448 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AR | NP77AR | np7 7ar | np77ar | Monmouthshire | Sir Fynwy | Llanwenarth STW | 441 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328593 | 214964 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AS | NP77AS | np7 7as | np77as | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1379 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329475 | 215283 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AT | NP77AT | np7 7at | np77at | Monmouthshire | Sir Fynwy | Llanwenarth STW | 518 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328695 | 214868 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AU | NP77AU | np7 7au | np77au | Monmouthshire | Sir Fynwy | Llanwenarth STW | 515 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328652 | 215015 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AW | NP77AW | np7 7aw | np77aw | Monmouthshire | Sir Fynwy | Llanwenarth STW | 395 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328561 | 214912 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AX | NP77AX | np7 7ax | np77ax | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1166 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329307 | 214513 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7AY | NP77AY | np7 7ay | np77ay | Monmouthshire | Sir Fynwy | Llanwenarth STW | 429 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328501 | 215094 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7BA | NP77BA | np7 7ba | np77ba | Monmouthshire | Sir Fynwy | Llanwenarth STW | 555 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328691 | 215026 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7BB | NP77BB | np7 7bb | np77bb | Monmouthshire | Sir Fynwy | Llanwenarth STW | 641 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328777 | 215044 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7BD | NP77BD | np7 7bd | np77bd | Monmouthshire | Sir Fynwy | Llanwenarth STW | 867 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328998 | 215096 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7BE | NP77BE | np7 7be | np77be | Monmouthshire | Sir Fynwy | Llanwenarth STW | 922 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329007 | 215218 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7BH | NP77BH | np7 7bh | np77bh | Monmouthshire | Sir Fynwy | Llanwenarth STW | 729 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328854 | 215088 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7BL | NP77BL | np7 7bl | np77bl | Monmouthshire | Sir Fynwy | Llanwenarth STW | 986 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329074 | 215226 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7BN | NP77BN | np7 7bn | np77bn | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1135 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329130 | 215430 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7BQ | NP77BQ | np7 7bq | np77bq | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1231 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329303 | 215313 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7BR | NP77BR | np7 7br | np77br | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1186 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329231 | 215358 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7BS | NP77BS | np7 7bs | np77bs | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1212 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329228 | 215418 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7BT | NP77BT | np7 7bt | np77bt | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1117 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329203 | 215257 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7BW | NP77BW | np7 7bw | np77bw | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1116 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329074 | 215478 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7DA | NP77DA | np7 7da | np77da | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1363 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329542 | 214843 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DB | NP77DB | np7 7db | np77db | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1127 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329290 | 215002 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DD | NP77DD | np7 7dd | np77dd | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1448 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329628 | 214808 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DE | NP77DE | np7 7de | np77de | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1251 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329381 | 215159 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DF | NP77DF | np7 7df | np77df | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1052 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329186 | 215116 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DG | NP77DG | np7 7dg | np77dg | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1144 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329323 | 214844 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DH | NP77DH | np7 7dh | np77dh | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1249 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329425 | 214718 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DL | NP77DL | np7 7dl | np77dl | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1302 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329475 | 214676 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DN | NP77DN | np7 7dn | np77dn | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1201 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329371 | 214658 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DP | NP77DP | np7 7dp | np77dp | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1148 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329326 | 214755 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DR | NP77DR | np7 7dr | np77dr | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1038 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329216 | 214864 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DS | NP77DS | np7 7ds | np77ds | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1053 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329226 | 214930 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DT | NP77DT | np7 7dt | np77dt | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1113 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329283 | 214663 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DU | NP77DU | np7 7du | np77du | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1035 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329213 | 214745 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DW | NP77DW | np7 7dw | np77dw | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1231 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329401 | 214656 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7DY | NP77DY | np7 7dy | np77dy | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1053 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329232 | 214767 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7EA | NP77EA | np7 7ea | np77ea | Monmouthshire | Sir Fynwy | Llanwenarth STW | 995 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329165 | 214673 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7EB | NP77EB | np7 7eb | np77eb | Monmouthshire | Sir Fynwy | Llanwenarth STW | 915 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329091 | 214889 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7ED | NP77ED | np7 7ed | np77ed | Monmouthshire | Sir Fynwy | Llanwenarth STW | 965 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329143 | 214862 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7EE | NP77EE | np7 7ee | np77ee | Monmouthshire | Sir Fynwy | Llanwenarth STW | 985 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329151 | 214649 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7EG | NP77EG | np7 7eg | np77eg | Monmouthshire | Sir Fynwy | Llanwenarth STW | 714 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 328817 | 214487 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7EH | NP77EH | np7 7eh | np77eh | Monmouthshire | Sir Fynwy | Llanwenarth STW | 549 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328716 | 214692 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7EJ | NP77EJ | np7 7ej | np77ej | Monmouthshire | Sir Fynwy | Llanwenarth STW | 613 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328781 | 214692 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7EL | NP77EL | np7 7el | np77el | Monmouthshire | Sir Fynwy | Llanwenarth STW | 380 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328558 | 214774 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7EN | NP77EN | np7 7en | np77en | Monmouthshire | Sir Fynwy | Llanwenarth STW | 294 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 328349 | 215050 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7EP | NP77EP | np7 7ep | np77ep | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1011 | 1061 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.78 | 10.55 | 11.66 | 327234 | 215260 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7ER | NP77ER | np7 7er | np77er | Monmouthshire | Sir Fynwy | Aberbaiden STW | 998 | 1113 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.74 | 11.06 | 12.23 | 326355 | 215776 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7ES | NP77ES | np7 7es | np77es | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1098 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 326762 | 215794 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7ET | NP77ET | np7 7et | np77et | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1281 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 326533 | 216045 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7EU | NP77EU | np7 7eu | np77eu | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1143 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 327214 | 215521 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7EW | NP77EW | np7 7ew | np77ew | Monmouthshire | Sir Fynwy | Llanwenarth STW | 413 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 328162 | 215222 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7EY | NP77EY | np7 7ey | np77ey | Monmouthshire | Sir Fynwy | Llanwenarth STW | 839 | 1048 | 900to1200 | 2.1 | 1.53 | 1.13 | 19.53 | 10.42 | 11.51 | 327787 | 215551 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7HA | NP77HA | np7 7ha | np77ha | Monmouthshire | Sir Fynwy | Llanwenarth STW | 658 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 328355 | 215444 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7HE | NP77HE | np7 7he | np77he | Monmouthshire | Sir Fynwy | Llanwenarth STW | 758 | 1048 | 900to1200 | 2.1 | 1.53 | 1.13 | 19.53 | 10.42 | 11.51 | 328364 | 215545 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7HF | NP77HF | np7 7hf | np77hf | Monmouthshire | Sir Fynwy | Llanwenarth STW | 471 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 328488 | 215166 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7HG | NP77HG | np7 7hg | np77hg | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1149 | 1076 | 900to1200 | 2.15 | 1.58 | 1.16 | 20.05 | 10.7 | 11.82 | 328782 | 215788 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7HH | NP77HH | np7 7hh | np77hh | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1248 | 1076 | 900to1200 | 2.15 | 1.58 | 1.16 | 20.05 | 10.7 | 11.82 | 329183 | 215552 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7HL | NP77HL | np7 7hl | np77hl | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1279 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329290 | 215445 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7HN | NP77HN | np7 7hn | np77hn | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2548 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330274 | 216261 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7HR | NP77HR | np7 7hr | np77hr | Monmouthshire | Sir Fynwy | Llanwenarth STW | 3380 | 1117 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.82 | 11.1 | 12.27 | 330168 | 217542 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7HS | NP77HS | np7 7hs | np77hs | Monmouthshire | Sir Fynwy | Cwmyoy STW | 3746 | 1117 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.82 | 11.1 | 12.27 | 330211 | 217985 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7HT | NP77HT | np7 7ht | np77ht | Monmouthshire | Sir Fynwy | Llanwenarth STW | 2333 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 330012 | 216254 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7HU | NP77HU | np7 7hu | np77hu | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1711 | 1076 | 900to1200 | 2.15 | 1.58 | 1.16 | 20.05 | 10.7 | 11.82 | 328739 | 216427 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7HY | NP77HY | np7 7hy | np77hy | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1785 | 1076 | 900to1200 | 2.15 | 1.58 | 1.16 | 20.05 | 10.7 | 11.82 | 329234 | 216250 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LA | NP77LA | np7 7la | np77la | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1720 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 327128 | 216309 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LE | NP77LE | np7 7le | np77le | Monmouthshire | Sir Fynwy | Cwmyoy STW | 2876 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 330804 | 218751 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LF | NP77LF | np7 7lf | np77lf | Monmouthshire | Sir Fynwy | Cwmyoy STW | 3216 | 1146 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.36 | 11.39 | 12.59 | 329745 | 218728 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LG | NP77LG | np7 7lg | np77lg | Monmouthshire | Sir Fynwy | Cwmyoy STW | 2687 | 1146 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.36 | 11.39 | 12.59 | 329758 | 219328 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LH | NP77LH | np7 7lh | np77lh | Monmouthshire | Sir Fynwy | Cwmyoy STW | 2576 | 1148 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.4 | 11.41 | 12.61 | 329117 | 220073 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LJ | NP77LJ | np7 7lj | np77lj | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1532 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 331043 | 220076 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LL | NP77LL | np7 7ll | np77ll | Monmouthshire | Sir Fynwy | Cwmyoy STW | 2458 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 328923 | 220653 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LN | NP77LN | np7 7ln | np77ln | Monmouthshire | Sir Fynwy | Cwmyoy STW | 3057 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 328288 | 220643 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LP | NP77LP | np7 7lp | np77lp | Powys | Powys | Cwmyoy STW | 3824 | 1263 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.54 | 12.55 | 13.88 | 327430 | 222287 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LR | NP77LR | np7 7lr | np77lr | Powys | Powys | Cwmyoy STW | 3186 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 328057 | 221025 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LS | NP77LS | np7 7ls | np77ls | Monmouthshire | Sir Fynwy | Cwmyoy STW | 2836 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 328416 | 221017 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LT | NP77LT | np7 7lt | np77lt | Monmouthshire | Sir Fynwy | Cwmyoy STW | 2512 | 1213 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.61 | 12.06 | 13.33 | 328690 | 221832 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LU | NP77LU | np7 7lu | np77lu | Monmouthshire | Sir Fynwy | Cwmyoy STW | 3614 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 328190 | 223613 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LW | NP77LW | np7 7lw | np77lw | Monmouthshire | Sir Fynwy | Llanbedr WwTW | 3329 | 1180 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.99 | 11.73 | 12.96 | 327118 | 220506 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LY | NP77LY | np7 7ly | np77ly | Powys | Powys | Llanbedr WwTW | 6131 | 1317 | 1200to1500 | 2.64 | 1.93 | 1.41 | 24.55 | 13.09 | 14.47 | 325833 | 225855 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NA | NP77NA | np7 7na | np77na | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1522 | 1145 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.34 | 11.38 | 12.58 | 329704 | 221272 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7RA | NP77RA | np7 7ra | np77ra | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1146 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329302 | 214579 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RB | NP77RB | np7 7rb | np77rb | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1008 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329151 | 214540 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RD | NP77RD | np7 7rd | np77rd | Monmouthshire | Sir Fynwy | Llanwenarth STW | 939 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329097 | 214608 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RE | NP77RE | np7 7re | np77re | Monmouthshire | Sir Fynwy | Llanwenarth STW | 767 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328930 | 214653 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RF | NP77RF | np7 7rf | np77rf | Monmouthshire | Sir Fynwy | Llanwenarth STW | 834 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 328981 | 214577 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RG | NP77RG | np7 7rg | np77rg | Monmouthshire | Sir Fynwy | Llanwenarth STW | 977 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329091 | 214457 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RH | NP77RH | np7 7rh | np77rh | Monmouthshire | Sir Fynwy | Llanwenarth STW | 915 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329038 | 214492 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RJ | NP77RJ | np7 7rj | np77rj | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1334 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329487 | 215076 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RL | NP77RL | np7 7rl | np77rl | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1065 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329128 | 214326 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RN | NP77RN | np7 7rn | np77rn | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1446 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329624 | 214882 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RQ | NP77RQ | np7 7rq | np77rq | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1003 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329035 | 214286 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RS | NP77RS | np7 7rs | np77rs | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1638 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 329686 | 215452 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RU | NP77RU | np7 7ru | np77ru | Monmouthshire | Sir Fynwy | Llanwenarth STW | 949 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329105 | 214601 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RW | NP77RW | np7 7rw | np77rw | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1313 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329393 | 215312 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RX | NP77RX | np7 7rx | np77rx | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1118 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329252 | 214495 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RY | NP77RY | np7 7ry | np77ry | Monmouthshire | Sir Fynwy | Llanwenarth STW | 945 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 329087 | 214547 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7RZ | NP77RZ | np7 7rz | np77rz | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1098 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329075 | 214175 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7SA | NP77SA | np7 7sa | np77sa | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1147 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329074 | 214092 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7WU | NP77WU | np7 7wu | np77wu | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8AE | NP78AE | np7 8ae | np78ae | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 3521 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 332889 | 215709 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8AR | NP78AR | np7 8ar | np78ar | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 3162 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 331860 | 215820 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8AT | NP78AT | np7 8at | np78at | Monmouthshire | Sir Fynwy | Cwmyoy STW | 4030 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 331477 | 217582 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8AU | NP78AU | np7 8au | np78au | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 3909 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 331721 | 216753 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8AY | NP78AY | np7 8ay | np78ay | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2204 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 331239 | 215081 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8BB | NP78BB | np7 8bb | np78bb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2393 | 1020 | 900to1200 | 2.04 | 1.49 | 1.1 | 19.01 | 10.14 | 11.21 | 331827 | 214843 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8BU | NP78BU | np7 8bu | np78bu | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2351 | 1038 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.35 | 10.32 | 11.4 | 332094 | 214420 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8BY | NP78BY | np7 8by | np78by | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1609 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 331064 | 214480 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8DE | NP78DE | np7 8de | np78de | Monmouthshire | Sir Fynwy | Llanwenarth STW | 3819 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 331056 | 217321 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8DF | NP78DF | np7 8df | np78df | Monmouthshire | Sir Fynwy | Cwmyoy STW | 3618 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 331195 | 217983 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8NF | NP78NF | np7 8nf | np78nf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2626 | 1020 | 900to1200 | 2.04 | 1.49 | 1.1 | 19.01 | 10.14 | 11.21 | 331539 | 215390 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NG | NP78NG | np7 8ng | np78ng | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2916 | 1020 | 900to1200 | 2.04 | 1.49 | 1.1 | 19.01 | 10.14 | 11.21 | 332101 | 215309 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NH | NP78NH | np7 8nh | np78nh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 3679 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 332433 | 216034 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8YA | NP78YA | np7 8ya | np78ya | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AA | NP79AA | np7 9aa | np79aa | Monmouthshire | Sir Fynwy | Llanellen STW | 1132 | 1139 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.23 | 11.32 | 12.51 | 331335 | 211607 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AB | NP79AB | np7 9ab | np79ab | Monmouthshire | Sir Fynwy | Llanellen STW | 1501 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 331782 | 211385 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AD | NP79AD | np7 9ad | np79ad | Monmouthshire | Sir Fynwy | Llanellen STW | 839 | 1126 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.99 | 11.19 | 12.37 | 331122 | 211318 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AE | NP79AE | np7 9ae | np79ae | Monmouthshire | Sir Fynwy | Bryn WwTW | 1079 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 332537 | 210400 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AF | NP79AF | np7 9af | np79af | Monmouthshire | Sir Fynwy | Bryn WwTW | 270 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 333149 | 209867 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AG | NP79AG | np7 9ag | np79ag | Monmouthshire | Sir Fynwy | Bryn WwTW | 331 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 333075 | 209854 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AH | NP79AH | np7 9ah | np79ah | Monmouthshire | Sir Fynwy | Bryn WwTW | 320 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 333124 | 209919 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AJ | NP79AJ | np7 9aj | np79aj | Monmouthshire | Sir Fynwy | Bryn WwTW | 160 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 333237 | 209797 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AL | NP79AL | np7 9al | np79al | Monmouthshire | Sir Fynwy | Bryn WwTW | 223 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 333216 | 209879 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AN | NP79AN | np7 9an | np79an | Monmouthshire | Sir Fynwy | Bryn WwTW | 167 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 333224 | 209783 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AP | NP79AP | np7 9ap | np79ap | Monmouthshire | Sir Fynwy | Bryn WwTW | 196 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 333186 | 209723 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AQ | NP79AQ | np7 9aq | np79aq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 527 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 329556 | 213241 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AR | NP79AR | np7 9ar | np79ar | Monmouthshire | Sir Fynwy | Bryn WwTW | 455 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 333464 | 210177 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AS | NP79AS | np7 9as | np79as | Monmouthshire | Sir Fynwy | Bryn WwTW | 724 | 1029 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.18 | 10.23 | 11.31 | 333525 | 210439 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AT | NP79AT | np7 9at | np79at | Monmouthshire | Sir Fynwy | Bryn WwTW | 492 | 1029 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.18 | 10.23 | 11.31 | 333653 | 210141 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AU | NP79AU | np7 9au | np79au | Monmouthshire | Sir Fynwy | Bryn WwTW | 1086 | 1029 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.18 | 10.23 | 11.31 | 334262 | 210365 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AW | NP79AW | np7 9aw | np79aw | Monmouthshire | Sir Fynwy | Bryn WwTW | 182 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 333200 | 209734 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AX | NP79AX | np7 9ax | np79ax | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 743 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329413 | 213529 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AY | NP79AY | np7 9ay | np79ay | Monmouthshire | Sir Fynwy | Bryn WwTW | 1386 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 334743 | 209471 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9AZ | NP79AZ | np7 9az | np79az | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 829 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329320 | 213533 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BA | NP79BA | np7 9ba | np79ba | Monmouthshire | Sir Fynwy | Bryn WwTW | 2113 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 335492 | 209626 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BB | NP79BB | np7 9bb | np79bb | Monmouthshire | Sir Fynwy | Llanvair STW | 1710 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 334678 | 208449 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BD | NP79BD | np7 9bd | np79bd | Monmouthshire | Sir Fynwy | Llanvair STW | 1102 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 334812 | 207855 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BE | NP79BE | np7 9be | np79be | Monmouthshire | Sir Fynwy | Llanvair STW | 1207 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 335199 | 207960 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BG | NP79BG | np7 9bg | np79bg | Monmouthshire | Sir Fynwy | Bryn WwTW | 1870 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 335161 | 209157 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BH | NP79BH | np7 9bh | np79bh | Monmouthshire | Sir Fynwy | Llanvair STW | 2433 | 1038 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.35 | 10.32 | 11.4 | 337065 | 208055 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BL | NP79BL | np7 9bl | np79bl | Monmouthshire | Sir Fynwy | Llanarth STW | 1337 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 336601 | 209853 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BN | NP79BN | np7 9bn | np79bn | Monmouthshire | Sir Fynwy | Llanarth STW | 1463 | 1013 | 900to1200 | 2.03 | 1.48 | 1.09 | 18.88 | 10.07 | 11.13 | 336372 | 210091 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BP | NP79BP | np7 9bp | np79bp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 388 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330338 | 212915 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BQ | NP79BQ | np7 9bq | np79bq | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1032 | 1139 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.23 | 11.32 | 12.51 | 327961 | 213802 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9BR | NP79BR | np7 9br | np79br | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1123 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328987 | 213455 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BS | NP79BS | np7 9bs | np79bs | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 749 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330425 | 212540 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BT | NP79BT | np7 9bt | np79bt | Monmouthshire | Sir Fynwy | Llanellen STW | 784 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 330458 | 211918 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BU | NP79BU | np7 9bu | np79bu | Monmouthshire | Sir Fynwy | Llanellen STW | 707 | 1126 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.99 | 11.19 | 12.37 | 330789 | 210640 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BW | NP79BW | np7 9bw | np79bw | Monmouthshire | Sir Fynwy | Llanarth STW | 1793 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 336710 | 209041 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BX | NP79BX | np7 9bx | np79bx | Monmouthshire | Sir Fynwy | Llanover STW | 1252 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 330728 | 209629 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BY | NP79BY | np7 9by | np79by | Monmouthshire | Sir Fynwy | Llanover STW | 609 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 331588 | 209849 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9BZ | NP79BZ | np7 9bz | np79bz | Monmouthshire | Sir Fynwy | Aberbaiden STW | 847 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326709 | 214013 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9DA | NP79DA | np7 9da | np79da | Monmouthshire | Sir Fynwy | Bryn WwTW | 610 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333002 | 209253 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DB | NP79DB | np7 9db | np79db | Monmouthshire | Sir Fynwy | Llanover STW | 947 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 332562 | 208638 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DD | NP79DD | np7 9dd | np79dd | Monmouthshire | Sir Fynwy | Bryn WwTW | 1019 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 333219 | 208724 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DE | NP79DE | np7 9de | np79de | Monmouthshire | Sir Fynwy | Llanvair STW | 1768 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 333669 | 207933 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DF | NP79DF | np7 9df | np79df | Monmouthshire | Sir Fynwy | Llanvair STW | 2050 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 332992 | 207177 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DG | NP79DG | np7 9dg | np79dg | Monmouthshire | Sir Fynwy | Llanvair STW | 2342 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 332673 | 207023 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DH | NP79DH | np7 9dh | np79dh | Monmouthshire | Sir Fynwy | Goytre STW | 2515 | 1245 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.2 | 12.38 | 13.68 | 332176 | 206466 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DL | NP79DL | np7 9dl | np79dl | Monmouthshire | Sir Fynwy | Goytre STW | 2810 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 331873 | 206512 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DN | NP79DN | np7 9dn | np79dn | Monmouthshire | Sir Fynwy | Goytre STW | 1397 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 333233 | 206082 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DP | NP79DP | np7 9dp | np79dp | Monmouthshire | Sir Fynwy | Goytre STW | 858 | 1117 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.82 | 11.1 | 12.27 | 333672 | 205756 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DQ | NP79DQ | np7 9dq | np79dq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1072 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329054 | 212903 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DR | NP79DR | np7 9dr | np79dr | Monmouthshire | Sir Fynwy | Goytre STW | 294 | 1117 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.82 | 11.1 | 12.27 | 334317 | 205665 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DS | NP79DS | np7 9ds | np79ds | Monmouthshire | Sir Fynwy | Goytre STW | 669 | 1078 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.09 | 10.72 | 11.84 | 334771 | 205994 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DT | NP79DT | np7 9dt | np79dt | Monmouthshire | Sir Fynwy | Llanvair STW | 308 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 334728 | 206625 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DU | NP79DU | np7 9du | np79du | Monmouthshire | Sir Fynwy | Llanvair STW | 301 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 334832 | 207020 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DW | NP79DW | np7 9dw | np79dw | Monmouthshire | Sir Fynwy | Goytre STW | 1790 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 332829 | 206153 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DX | NP79DX | np7 9dx | np79dx | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1075 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329058 | 212880 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9DY | NP79DY | np7 9dy | np79dy | Monmouthshire | Sir Fynwy | Llanvair STW | 615 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 334612 | 207247 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9EA | NP79EA | np7 9ea | np79ea | Monmouthshire | Sir Fynwy | Llanvair STW | 393 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 334813 | 207116 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9EB | NP79EB | np7 9eb | np79eb | Monmouthshire | Sir Fynwy | Llanover STW | 1271 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 330711 | 209641 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9ED | NP79ED | np7 9ed | np79ed | Monmouthshire | Sir Fynwy | Llanover STW | 109 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 331975 | 209254 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9EF | NP79EF | np7 9ef | np79ef | Monmouthshire | Sir Fynwy | Llanover STW | 1122 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 331890 | 208240 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9EG | NP79EG | np7 9eg | np79eg | Monmouthshire | Sir Fynwy | Llanover STW | 1990 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 331756 | 207380 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9EH | NP79EH | np7 9eh | np79eh | Monmouthshire | Sir Fynwy | Llanover STW | 2345 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 331833 | 207019 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9EJ | NP79EJ | np7 9ej | np79ej | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1066 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329046 | 212958 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9EL | NP79EL | np7 9el | np79el | Monmouthshire | Sir Fynwy | Llanover STW | 2400 | 1324 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.68 | 13.16 | 14.55 | 331225 | 207073 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9EN | NP79EN | np7 9en | np79en | Monmouthshire | Sir Fynwy | Llanover STW | 1729 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 331446 | 207707 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9EP | NP79EP | np7 9ep | np79ep | Monmouthshire | Sir Fynwy | Llanover STW | 2935 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 330209 | 206998 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9EQ | NP79EQ | np7 9eq | np79eq | Monmouthshire | Sir Fynwy | Llanover STW | 2748 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 329334 | 208522 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9ER | NP79ER | np7 9er | np79er | Monmouthshire | Sir Fynwy | Llanover STW | 3496 | 1524 | Over1500 | 3.05 | 2.23 | 1.64 | 28.4 | 15.15 | 16.74 | 329121 | 207308 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9ES | NP79ES | np7 9es | np79es | Monmouthshire | Sir Fynwy | Llanover STW | 2237 | 1356 | 1200to1500 | 2.71 | 1.99 | 1.46 | 25.27 | 13.48 | 14.9 | 330084 | 208127 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9ET | NP79ET | np7 9et | np79et | Monmouthshire | Sir Fynwy | Llanellen STW | 3837 | 1564 | Over1500 | 3.13 | 2.29 | 1.68 | 29.15 | 15.55 | 17.18 | 328061 | 208035 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9EU | NP79EU | np7 9eu | np79eu | Monmouthshire | Sir Fynwy | Llanover STW | 1526 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 331328 | 207967 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9EW | NP79EW | np7 9ew | np79ew | Monmouthshire | Sir Fynwy | Llanover STW | 3163 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 330994 | 206346 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9EX | NP79EX | np7 9ex | np79ex | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1202 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 326156 | 213592 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9EY | NP79EY | np7 9ey | np79ey | Monmouthshire | Sir Fynwy | Llanover STW | 1385 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 331278 | 208150 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9FD | NP79FD | np7 9fd | np79fd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 996 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329098 | 213057 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9FE | NP79FE | np7 9fe | np79fe | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1041 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329045 | 213122 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9FF | NP79FF | np7 9ff | np79ff | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1037 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329062 | 213019 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9FJ | NP79FJ | np7 9fj | np79fj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 910 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329175 | 213135 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9FL | NP79FL | np7 9fl | np79fl | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 962 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329124 | 213127 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HA | NP79HA | np7 9ha | np79ha | Monmouthshire | Sir Fynwy | Llanover STW | 1429 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 331090 | 208219 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HB | NP79HB | np7 9hb | np79hb | Monmouthshire | Sir Fynwy | Llanover STW | 1489 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 331120 | 208125 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HD | NP79HD | np7 9hd | np79hd | Monmouthshire | Sir Fynwy | Llanover STW | 1480 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 331453 | 207967 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HE | NP79HE | np7 9he | np79he | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 946 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 329625 | 212378 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HF | NP79HF | np7 9hf | np79hf | Monmouthshire | Sir Fynwy | Llanellen STW | 736 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 329679 | 211544 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HG | NP79HG | np7 9hg | np79hg | Monmouthshire | Sir Fynwy | Llanellen STW | 595 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 329729 | 210982 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HH | NP79HH | np7 9hh | np79hh | Monmouthshire | Sir Fynwy | Llanellen STW | 169 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 330198 | 211015 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HJ | NP79HJ | np7 9hj | np79hj | Monmouthshire | Sir Fynwy | Llanellen STW | 383 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 330025 | 210884 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HN | NP79HN | np7 9hn | np79hn | Monmouthshire | Sir Fynwy | Llanellen STW | 271 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 330171 | 210912 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HP | NP79HP | np7 9hp | np79hp | Monmouthshire | Sir Fynwy | Llanellen STW | 332 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 330313 | 210818 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HR | NP79HR | np7 9hr | np79hr | Monmouthshire | Sir Fynwy | Llanellen STW | 285 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 330397 | 210882 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HS | NP79HS | np7 9hs | np79hs | Monmouthshire | Sir Fynwy | Llanellen STW | 1205 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 330653 | 209998 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HT | NP79HT | np7 9ht | np79ht | Monmouthshire | Sir Fynwy | Llanellen STW | 605 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 330316 | 210545 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HU | NP79HU | np7 9hu | np79hu | Monmouthshire | Sir Fynwy | Llanover STW | 1400 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 330551 | 209409 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HW | NP79HW | np7 9hw | np79hw | Monmouthshire | Sir Fynwy | Llanellen STW | 400 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 330160 | 210775 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9HY | NP79HY | np7 9hy | np79hy | Monmouthshire | Sir Fynwy | Llanover STW | 1212 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 330745 | 209235 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9JA | NP79JA | np7 9ja | np79ja | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 236 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330275 | 213071 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9JB | NP79JB | np7 9jb | np79jb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 344 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330378 | 213030 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9JD | NP79JD | np7 9jd | np79jd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 298 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330301 | 213004 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9JE | NP79JE | np7 9je | np79je | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 248 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330238 | 213013 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9JF | NP79JF | np7 9jf | np79jf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 260 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330341 | 213221 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9JG | NP79JG | np7 9jg | np79jg | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 196 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330267 | 213141 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9JH | NP79JH | np7 9jh | np79jh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 293 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330372 | 213167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9JJ | NP79JJ | np7 9jj | np79jj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 316 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330381 | 213104 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9JL | NP79JL | np7 9jl | np79jl | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 184 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330266 | 213199 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9JN | NP79JN | np7 9jn | np79jn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 201 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330277 | 213255 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9JZ | NP79JZ | np7 9jz | np79jz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1232 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328851 | 213167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LA | NP79LA | np7 9la | np79la | Monmouthshire | Sir Fynwy | Llanover STW | 1921 | 1341 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.99 | 13.33 | 14.73 | 330084 | 208906 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9LB | NP79LB | np7 9lb | np79lb | Monmouthshire | Sir Fynwy | Llanellen STW | 2565 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 328677 | 209165 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9LD | NP79LD | np7 9ld | np79ld | Monmouthshire | Sir Fynwy | Llanellen STW | 1771 | 1367 | 1200to1500 | 2.74 | 2 | 1.47 | 25.48 | 13.59 | 15.02 | 328961 | 209992 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9LE | NP79LE | np7 9le | np79le | Monmouthshire | Sir Fynwy | Llanellen STW | 1592 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 328851 | 211807 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9LF | NP79LF | np7 9lf | np79lf | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1301 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 328704 | 213620 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LH | NP79LH | np7 9lh | np79lh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 862 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329234 | 213357 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LJ | NP79LJ | np7 9lj | np79lj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1055 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329041 | 213374 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LL | NP79LL | np7 9ll | np79ll | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1044 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329221 | 213796 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LN | NP79LN | np7 9ln | np79ln | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1117 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328968 | 213282 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LP | NP79LP | np7 9lp | np79lp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1434 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328655 | 213347 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LQ | NP79LQ | np7 9lq | np79lq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 635 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329458 | 213325 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LR | NP79LR | np7 9lr | np79lr | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1282 | 1139 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.23 | 11.32 | 12.51 | 328297 | 213534 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LS | NP79LS | np7 9ls | np79ls | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1061 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329022 | 213174 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LT | NP79LT | np7 9lt | np79lt | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1132 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328950 | 213202 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LU | NP79LU | np7 9lu | np79lu | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1206 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328876 | 213217 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LX | NP79LX | np7 9lx | np79lx | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1349 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328742 | 213357 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LY | NP79LY | np7 9ly | np79ly | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1212 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328881 | 213045 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9LZ | NP79LZ | np7 9lz | np79lz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 873 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329339 | 213664 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NA | NP79NA | np7 9na | np79na | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1160 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328951 | 212952 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NB | NP79NB | np7 9nb | np79nb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1140 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328960 | 213004 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9ND | NP79ND | np7 9nd | np79nd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1277 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328849 | 212876 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NE | NP79NE | np7 9ne | np79ne | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1285 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328797 | 213207 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NF | NP79NF | np7 9nf | np79nf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1317 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328769 | 213110 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NG | NP79NG | np7 9ng | np79ng | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1636 | 1281 | 1200to1500 | 2.56 | 1.88 | 1.38 | 23.88 | 12.73 | 14.07 | 328456 | 213030 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9NH | NP79NH | np7 9nh | np79nh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1250 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328838 | 213320 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NJ | NP79NJ | np7 9nj | np79nj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 914 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329169 | 213243 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NL | NP79NL | np7 9nl | np79nl | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1238 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328858 | 213390 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NN | NP79NN | np7 9nn | np79nn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1200 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328892 | 213358 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NP | NP79NP | np7 9np | np79np | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1177 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328921 | 213397 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NQ | NP79NQ | np7 9nq | np79nq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 895 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329191 | 213289 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NR | NP79NR | np7 9nr | np79nr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1189 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328906 | 213376 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NS | NP79NS | np7 9ns | np79ns | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1222 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328863 | 213282 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NT | NP79NT | np7 9nt | np79nt | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1308 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326863 | 213577 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9NU | NP79NU | np7 9nu | np79nu | Monmouthshire | Sir Fynwy | Llanwenarth STW | 853 | 1139 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.23 | 11.32 | 12.51 | 327672 | 214125 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9NW | NP79NW | np7 9nw | np79nw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1154 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328950 | 213429 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NX | NP79NX | np7 9nx | np79nx | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1146 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328975 | 213500 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9NY | NP79NY | np7 9ny | np79ny | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1369 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 327067 | 213615 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9NZ | NP79NZ | np7 9nz | np79nz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 870 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329214 | 213258 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9PA | NP79PA | np7 9pa | np79pa | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1436 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 327276 | 213685 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PB | NP79PB | np7 9pb | np79pb | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1796 | 1281 | 1200to1500 | 2.56 | 1.88 | 1.38 | 23.88 | 12.73 | 14.07 | 327925 | 213033 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PD | NP79PD | np7 9pd | np79pd | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1310 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326974 | 213629 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PE | NP79PE | np7 9pe | np79pe | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1095 | 1139 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.23 | 11.32 | 12.51 | 328062 | 213722 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PF | NP79PF | np7 9pf | np79pf | Monmouthshire | Sir Fynwy | Llanwenarth STW | 1103 | 1139 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.23 | 11.32 | 12.51 | 327567 | 213894 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PG | NP79PG | np7 9pg | np79pg | Monmouthshire | Sir Fynwy | Aberbaiden STW | 818 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326793 | 214093 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PH | NP79PH | np7 9ph | np79ph | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1150 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326972 | 213814 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PJ | NP79PJ | np7 9pj | np79pj | Monmouthshire | Sir Fynwy | Aberbaiden STW | 881 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326890 | 214086 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PL | NP79PL | np7 9pl | np79pl | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1070 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326880 | 213851 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PN | NP79PN | np7 9pn | np79pn | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1153 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326902 | 213768 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PP | NP79PP | np7 9pp | np79pp | Monmouthshire | Sir Fynwy | Aberbaiden STW | 966 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326860 | 213961 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PQ | NP79PQ | np7 9pq | np79pq | Monmouthshire | Sir Fynwy | Aberbaiden STW | 882 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326647 | 213949 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PR | NP79PR | np7 9pr | np79pr | Monmouthshire | Sir Fynwy | Aberbaiden STW | 870 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326758 | 214012 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PS | NP79PS | np7 9ps | np79ps | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1089 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 327068 | 213963 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PT | NP79PT | np7 9pt | np79pt | Monmouthshire | Sir Fynwy | Aberbaiden STW | 950 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326664 | 213883 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PU | NP79PU | np7 9pu | np79pu | Monmouthshire | Sir Fynwy | Aberbaiden STW | 964 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326728 | 213893 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PW | NP79PW | np7 9pw | np79pw | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1076 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326924 | 213871 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PX | NP79PX | np7 9px | np79px | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 916 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329325 | 213721 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9PY | NP79PY | np7 9py | np79py | Monmouthshire | Sir Fynwy | Aberbaiden STW | 958 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326534 | 213839 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9PZ | NP79PZ | np7 9pz | np79pz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 772 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329460 | 213662 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9QA | NP79QA | np7 9qa | np79qa | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 722 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329447 | 213550 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9QB | NP79QB | np7 9qb | np79qb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 897 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329264 | 213573 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9QD | NP79QD | np7 9qd | np79qd | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 833 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 329342 | 213587 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9QF | NP79QF | np7 9qf | np79qf | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 806 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 329278 | 213151 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9QZ | NP79QZ | np7 9qz | np79qz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 374 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330449 | 213276 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9RA | NP79RA | np7 9ra | np79ra | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1088 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326778 | 213780 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RB | NP79RB | np7 9rb | np79rb | Monmouthshire | Sir Fynwy | Aberbaiden STW | 998 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326574 | 213807 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RD | NP79RD | np7 9rd | np79rd | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1042 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326545 | 213756 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RE | NP79RE | np7 9re | np79re | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1065 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326634 | 213753 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RF | NP79RF | np7 9rf | np79rf | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1014 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326736 | 213842 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RG | NP79RG | np7 9rg | np79rg | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1124 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326549 | 213673 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RH | NP79RH | np7 9rh | np79rh | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1279 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326635 | 213533 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RJ | NP79RJ | np7 9rj | np79rj | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1145 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326657 | 213676 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RL | NP79RL | np7 9rl | np79rl | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1249 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326785 | 213609 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RN | NP79RN | np7 9rn | np79rn | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1290 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326526 | 213501 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RP | NP79RP | np7 9rp | np79rp | Monmouthshire | Sir Fynwy | Aberbaiden STW | 940 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 326472 | 213847 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RQ | NP79RQ | np7 9rq | np79rq | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1285 | 1234 | 1200to1500 | 2.47 | 1.81 | 1.33 | 23 | 12.27 | 13.56 | 326439 | 213497 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RR | NP79RR | np7 9rr | np79rr | Monmouthshire | Sir Fynwy | Aberbaiden STW | 976 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 326301 | 213803 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RS | NP79RS | np7 9rs | np79rs | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1284 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 326113 | 213516 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RT | NP79RT | np7 9rt | np79rt | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1537 | 1266 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.6 | 12.58 | 13.91 | 325359 | 213601 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RU | NP79RU | np7 9ru | np79ru | Monmouthshire | Sir Fynwy | Aberbaiden STW | 2184 | 1302 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.27 | 12.94 | 14.3 | 324977 | 213077 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RW | NP79RW | np7 9rw | np79rw | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1520 | 1278 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.82 | 12.7 | 14.04 | 326566 | 213275 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RX | NP79RX | np7 9rx | np79rx | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1186 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 326439 | 213596 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RY | NP79RY | np7 9ry | np79ry | Monmouthshire | Sir Fynwy | Aberbaiden STW | 2264 | 1234 | 1200to1500 | 2.47 | 1.81 | 1.33 | 23 | 12.27 | 13.56 | 325711 | 212606 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9RZ | NP79RZ | np7 9rz | np79rz | Monmouthshire | Sir Fynwy | Aberbaiden STW | 1302 | 1234 | 1200to1500 | 2.47 | 1.81 | 1.33 | 23 | 12.27 | 13.56 | 326138 | 213493 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9SA | NP79SA | np7 9sa | np79sa | Monmouthshire | Sir Fynwy | Aberbaiden STW | 766 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326621 | 214063 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9SB | NP79SB | np7 9sb | np79sb | Monmouthshire | Sir Fynwy | Aberbaiden STW | 779 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 326680 | 214075 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9SD | NP79SD | np7 9sd | np79sd | Monmouthshire | Sir Fynwy | Aberbaiden STW | 851 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 327081 | 214349 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9SE | NP79SE | np7 9se | np79se | Monmouthshire | Sir Fynwy | Aberbaiden STW | 418 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 326211 | 214383 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9SF | NP79SF | np7 9sf | np79sf | Monmouthshire | Sir Fynwy | Aberbaiden STW | 987 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 325824 | 213941 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9SG | NP79SG | np7 9sg | np79sg | Monmouthshire | Sir Fynwy | Llanwenarth STW | 717 | 1139 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.23 | 11.32 | 12.51 | 328061 | 214103 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 9SH | NP79SH | np7 9sh | np79sh | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1312 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 330862 | 214260 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9SJ | NP79SJ | np7 9sj | np79sj | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 405 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330470 | 213322 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9SL | NP79SL | np7 9sl | np79sl | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1264 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 331054 | 214013 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9SN | NP79SN | np7 9sn | np79sn | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1118 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 331117 | 213627 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9SP | NP79SP | np7 9sp | np79sp | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 415 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330495 | 213165 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9SQ | NP79SQ | np7 9sq | np79sq | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 410 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330451 | 213384 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9SR | NP79SR | np7 9sr | np79sr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 468 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330498 | 212992 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9SS | NP79SS | np7 9ss | np79ss | Monmouthshire | Sir Fynwy | Llanellen STW | 1220 | 1139 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.23 | 11.32 | 12.51 | 330850 | 212239 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9ST | NP79ST | np7 9st | np79st | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1409 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 331362 | 212617 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9SU | NP79SU | np7 9su | np79su | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1760 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 331610 | 212334 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9SW | NP79SW | np7 9sw | np79sw | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 314 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330343 | 213380 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9SX | NP79SX | np7 9sx | np79sx | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 443 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330485 | 213390 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9SY | NP79SY | np7 9sy | np79sy | Monmouthshire | Sir Fynwy | Bryn WwTW | 2479 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 332639 | 212094 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9SZ | NP79SZ | np7 9sz | np79sz | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 417 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330499 | 213196 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TA | NP79TA | np7 9ta | np79ta | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2230 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 332243 | 212660 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TD | NP79TD | np7 9td | np79td | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2253 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 332333 | 213284 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TE | NP79TE | np7 9te | np79te | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 2192 | 1042 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.42 | 10.36 | 11.45 | 333043 | 212936 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TF | NP79TF | np7 9tf | np79tf | Monmouthshire | Sir Fynwy | Llanellen STW | 2617 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 332597 | 212403 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TG | NP79TG | np7 9tg | np79tg | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 1716 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 333784 | 212158 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UD | NP79UD | np7 9ud | np79ud | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 1377 | 1032 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.23 | 10.26 | 11.34 | 335775 | 211816 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UE | NP79UE | np7 9ue | np79ue | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 1494 | 1032 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.23 | 10.26 | 11.34 | 336186 | 211932 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UF | NP79UF | np7 9uf | np79uf | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 1843 | 1026 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.12 | 10.2 | 11.27 | 336162 | 211491 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UG | NP79UG | np7 9ug | np79ug | Monmouthshire | Sir Fynwy | Llanarth STW | 1769 | 1026 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.12 | 10.2 | 11.27 | 336183 | 211231 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UH | NP79UH | np7 9uh | np79uh | Monmouthshire | Sir Fynwy | Llanarth STW | 1512 | 1026 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.12 | 10.2 | 11.27 | 336310 | 210816 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UL | NP79UL | np7 9ul | np79ul | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 1730 | 1030 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.2 | 10.24 | 11.32 | 335360 | 211355 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UN | NP79UN | np7 9un | np79un | Monmouthshire | Sir Fynwy | Bryn WwTW | 1458 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 334776 | 210155 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UP | NP79UP | np7 9up | np79up | Monmouthshire | Sir Fynwy | Bryn WwTW | 1499 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 334783 | 210263 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UR | NP79UR | np7 9ur | np79ur | Monmouthshire | Sir Fynwy | Bryn WwTW | 1826 | 1030 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.2 | 10.24 | 11.32 | 334912 | 210725 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UT | NP79UT | np7 9ut | np79ut | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 1436 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 334673 | 211757 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UU | NP79UU | np7 9uu | np79uu | Monmouthshire | Sir Fynwy | Bryn WwTW | 1916 | 1030 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.2 | 10.24 | 11.32 | 334581 | 211223 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UW | NP79UW | np7 9uw | np79uw | Monmouthshire | Sir Fynwy | Bryn WwTW | 1533 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 334804 | 210302 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UY | NP79UY | np7 9uy | np79uy | Monmouthshire | Sir Fynwy | Bryn WwTW | 1721 | 1034 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.27 | 10.28 | 11.36 | 333707 | 211419 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9WY | NP79WY | np7 9wy | np79wy | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 995 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 329824 | 214167 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9YA | NP79YA | np7 9ya | np79ya | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1347 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328735 | 213213 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9YB | NP79YB | np7 9yb | np79yb | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 1198 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 328889 | 213314 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9YD | NP79YD | np7 9yd | np79yd | Monmouthshire | Sir Fynwy | Llanover STW | 1030 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 330933 | 209197 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9YE | NP79YE | np7 9ye | np79ye | Monmouthshire | Sir Fynwy | Llanvair STW | 389 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 334895 | 207144 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9YF | NP79YF | np7 9yf | np79yf | Monmouthshire | Sir Fynwy | Llanvair STW | 315 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 334894 | 207067 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9YR | NP79YR | np7 9yr | np79yr | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 494 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 330217 | 212731 | Monmouthshire LPA | SO | River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council
NP8 1AD | NP81AD | np8 1ad | np81ad | Powys | Powys | Crickhowell STW | 1129 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321816 | 218366 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AE | NP81AE | np8 1ae | np81ae | Powys | Powys | Crickhowell STW | 1065 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321879 | 218334 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AF | NP81AF | np8 1af | np81af | Powys | Powys | Crickhowell STW | 1007 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321977 | 218330 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AG | NP81AG | np8 1ag | np81ag | Powys | Powys | Crickhowell STW | 921 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 322005 | 218245 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AJ | NP81AJ | np8 1aj | np81aj | Powys | Powys | Crickhowell STW | 885 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 322099 | 218259 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AL | NP81AL | np8 1al | np81al | Powys | Powys | Crickhowell STW | 865 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321986 | 218164 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AN | NP81AN | np8 1an | np81an | Powys | Powys | Crickhowell STW | 749 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 322201 | 218157 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AP | NP81AP | np8 1ap | np81ap | Powys | Powys | Crickhowell STW | 879 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321904 | 218113 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AQ | NP81AQ | np8 1aq | np81aq | Powys | Powys | Crickhowell STW | 975 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 322007 | 218310 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AR | NP81AR | np8 1ar | np81ar | Powys | Powys | Crickhowell STW | 1203 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321570 | 218228 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AS | NP81AS | np8 1as | np81as | Powys | Powys | Crickhowell STW | 1226 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321600 | 218299 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AT | NP81AT | np8 1at | np81at | Powys | Powys | Crickhowell STW | 1408 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321752 | 218661 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AU | NP81AU | np8 1au | np81au | Powys | Powys | Crickhowell STW | 1322 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321596 | 218431 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AW | NP81AW | np8 1aw | np81aw | Powys | Powys | Crickhowell STW | 1537 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321531 | 218661 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1AY | NP81AY | np8 1ay | np81ay | Powys | Powys | Crickhowell STW | 1270 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321560 | 218320 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BA | NP81BA | np8 1ba | np81ba | Powys | Powys | Crickhowell STW | 1364 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321566 | 218461 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BB | NP81BB | np8 1bb | np81bb | Powys | Powys | Crickhowell STW | 1241 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321693 | 218410 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BD | NP81BD | np8 1bd | np81bd | Powys | Powys | Crickhowell STW | 1211 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321765 | 218430 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BE | NP81BE | np8 1be | np81be | Powys | Powys | Crickhowell STW | 1157 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321711 | 218313 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BG | NP81BG | np8 1bg | np81bg | Powys | Powys | Crickhowell STW | 1182 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321650 | 218288 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BH | NP81BH | np8 1bh | np81bh | Powys | Powys | Crickhowell STW | 1179 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321774 | 218397 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BJ | NP81BJ | np8 1bj | np81bj | Powys | Powys | Crickhowell STW | 1249 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321704 | 218430 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BL | NP81BL | np8 1bl | np81bl | Powys | Powys | Crickhowell STW | 1143 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321786 | 218360 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BN | NP81BN | np8 1bn | np81bn | Powys | Powys | Crickhowell STW | 1097 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321866 | 218364 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BP | NP81BP | np8 1bp | np81bp | Powys | Powys | Crickhowell STW | 1156 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321888 | 218450 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BQ | NP81BQ | np8 1bq | np81bq | Powys | Powys | Crickhowell STW | 1106 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321808 | 218331 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BR | NP81BR | np8 1br | np81br | Powys | Powys | Crickhowell STW | 1620 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 322065 | 219031 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BT | NP81BT | np8 1bt | np81bt | Powys | Powys | Crickhowell STW | 1393 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321921 | 218737 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BU | NP81BU | np8 1bu | np81bu | Powys | Powys | Crickhowell STW | 1455 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321504 | 218528 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BW | NP81BW | np8 1bw | np81bw | Powys | Powys | Crickhowell STW | 1249 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321789 | 218495 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BX | NP81BX | np8 1bx | np81bx | Powys | Powys | Crickhowell STW | 1098 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 322013 | 218454 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BY | NP81BY | np8 1by | np81by | Powys | Powys | Crickhowell STW | 1419 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 322107 | 218834 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1BZ | NP81BZ | np8 1bz | np81bz | Powys | Powys | Crickhowell STW | 1201 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321954 | 218539 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DA | NP81DA | np8 1da | np81da | Powys | Powys | Crickhowell STW | 1561 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 322050 | 218965 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DB | NP81DB | np8 1db | np81db | Powys | Powys | Crickhowell STW | 1620 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321927 | 218985 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DD | NP81DD | np8 1dd | np81dd | Powys | Powys | Crickhowell STW | 1357 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321976 | 218722 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DE | NP81DE | np8 1de | np81de | Powys | Powys | Crickhowell STW | 1349 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321740 | 218583 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DF | NP81DF | np8 1df | np81df | Powys | Powys | Crickhowell STW | 486 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 322214 | 217861 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DG | NP81DG | np8 1dg | np81dg | Powys | Powys | Crickhowell STW | 1606 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321631 | 218819 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DH | NP81DH | np8 1dh | np81dh | Powys | Powys | Crickhowell STW | 1687 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321511 | 218835 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DJ | NP81DJ | np8 1dj | np81dj | Powys | Powys | Crickhowell STW | 1804 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 321433 | 218923 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DL | NP81DL | np8 1dl | np81dl | Powys | Powys | Crickhowell STW | 1925 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 321377 | 219032 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DN | NP81DN | np8 1dn | np81dn | Powys | Powys | Crickhowell STW | 1851 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 321484 | 219016 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DP | NP81DP | np8 1dp | np81dp | Powys | Powys | Crickhowell STW | 1532 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321766 | 218814 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DQ | NP81DQ | np8 1dq | np81dq | Powys | Powys | Crickhowell STW | 1427 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 322161 | 218857 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DR | NP81DR | np8 1dr | np81dr | Powys | Powys | Crickhowell STW | 1632 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321791 | 218940 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DS | NP81DS | np8 1ds | np81ds | Powys | Powys | Crickhowell STW | 1794 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321808 | 219125 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DT | NP81DT | np8 1dt | np81dt | Powys | Powys | Crickhowell STW | 1215 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321698 | 218380 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DU | NP81DU | np8 1du | np81du | Powys | Powys | Crickhowell STW | 1676 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321787 | 218986 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DW | NP81DW | np8 1dw | np81dw | Powys | Powys | Crickhowell STW | 1400 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321846 | 218707 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DX | NP81DX | np8 1dx | np81dx | Powys | Powys | Crickhowell STW | 1813 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321708 | 219100 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DY | NP81DY | np8 1dy | np81dy | Powys | Powys | Crickhowell STW | 1794 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321599 | 219020 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1DZ | NP81DZ | np8 1dz | np81dz | Powys | Powys | Dan Y Parc Highways Depot STW | 1507 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 320949 | 217910 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EB | NP81EB | np8 1eb | np81eb | Powys | Powys | Crickhowell STW | 491 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 322253 | 217894 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1ED | NP81ED | np8 1ed | np81ed | Powys | Powys | Crickhowell STW | 518 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 322961 | 217226 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EE | NP81EE | np8 1ee | np81ee | Powys | Powys | Glangrwyney STW | 880 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 323333 | 216631 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EF | NP81EF | np8 1ef | np81ef | Powys | Powys | Glangrwyney STW | 311 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 323851 | 216386 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EG | NP81EG | np8 1eg | np81eg | Powys | Powys | Glangrwyney STW | 251 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 323888 | 216335 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EH | NP81EH | np8 1eh | np81eh | Powys | Powys | Glangrwyney STW | 214 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 323929 | 216328 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EL | NP81EL | np8 1el | np81el | Powys | Powys | Glangrwyney STW | 195 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 323970 | 216345 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EN | NP81EN | np8 1en | np81en | Powys | Powys | Glangrwyney STW | 190 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 324006 | 216365 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EP | NP81EP | np8 1ep | np81ep | Monmouthshire | Sir Fynwy | Glangrwyney STW | 1349 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 325441 | 216062 | Brecon Beacons National Park LPA | SO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EQ | NP81EQ | np8 1eq | np81eq | Powys | Powys | Dan Y Parc Highways Depot STW | 1374 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 320778 | 217074 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1ER | NP81ER | np8 1er | np81er | Powys | Powys | Crickhowell STW | 813 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 322029 | 218131 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1ES | NP81ES | np8 1es | np81es | Powys | Powys | Glangrwyney STW | 343 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 324263 | 216502 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1ET | NP81ET | np8 1et | np81et | Powys | Powys | Glangrwyney STW | 514 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 324137 | 216712 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EU | NP81EU | np8 1eu | np81eu | Powys | Powys | Llangenny STW | 1274 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 325318 | 217796 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EW | NP81EW | np8 1ew | np81ew | Powys | Powys | Glangrwyney STW | 130 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 323994 | 216276 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EX | NP81EX | np8 1ex | np81ex | Powys | Powys | Crickhowell STW | 732 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 322141 | 218107 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EY | NP81EY | np8 1ey | np81ey | Powys | Powys | Llangenny STW | 786 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 324046 | 217134 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1EZ | NP81EZ | np8 1ez | np81ez | Powys | Powys | Crickhowell STW | 1213 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 322040 | 218592 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HA | NP81HA | np8 1ha | np81ha | Powys | Powys | Llangenny STW | 222 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 323963 | 218124 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HB | NP81HB | np8 1hb | np81hb | Powys | Powys | Crickhowell STW | 670 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 322980 | 217946 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HD | NP81HD | np8 1hd | np81hd | Powys | Powys | Llangenny STW | 22 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 324062 | 217939 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HE | NP81HE | np8 1he | np81he | Powys | Powys | Llangenny STW | 247 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 324233 | 218086 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HF | NP81HF | np8 1hf | np81hf | Powys | Powys | Llangenny STW | 1225 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 324637 | 218995 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HG | NP81HG | np8 1hg | np81hg | Powys | Powys | Crickhowell STW | 1227 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321413 | 218029 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HH | NP81HH | np8 1hh | np81hh | Powys | Powys | Crickhowell STW | 1103 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321519 | 217964 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HL | NP81HL | np8 1hl | np81hl | Powys | Powys | Crickhowell STW | 977 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 321633 | 217912 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HN | NP81HN | np8 1hn | np81hn | Powys | Powys | Crickhowell STW | 331 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 322190 | 217570 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HQ | NP81HQ | np8 1hq | np81hq | Powys | Powys | Dan Y Parc Highways Depot STW | 1340 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 320929 | 217552 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HS | NP81HS | np8 1hs | np81hs | Powys | Powys | Dan Y Parc Highways Depot STW | 45 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 322111 | 216978 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HT | NP81HT | np8 1ht | np81ht | Powys | Powys | Dan Y Parc Highways Depot STW | 733 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 321450 | 217215 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HU | NP81HU | np8 1hu | np81hu | Powys | Powys | Dan Y Parc Highways Depot STW | 1327 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 320991 | 217645 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HW | NP81HW | np8 1hw | np81hw | Powys | Powys | Dan Y Parc Highways Depot STW | 482 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 321936 | 217432 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1HY | NP81HY | np8 1hy | np81hy | Powys | Powys | Dan Y Parc Highways Depot STW | 1236 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321043 | 217549 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LA | NP81LA | np8 1la | np81la | Powys | Powys | Dan Y Parc Highways Depot STW | 1292 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 320930 | 217423 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LB | NP81LB | np8 1lb | np81lb | Powys | Powys | Dan Y Parc Highways Depot STW | 1202 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 320991 | 217317 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LD | NP81LD | np8 1ld | np81ld | Powys | Powys | Dan Y Parc Highways Depot STW | 1390 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 320784 | 217254 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LE | NP81LE | np8 1le | np81le | Powys | Powys | Dan Y Parc Highways Depot STW | 2068 | 1326 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.71 | 13.18 | 14.57 | 320096 | 217238 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LF | NP81LF | np8 1lf | np81lf | Powys | Powys | Dan Y Parc Highways Depot STW | 1792 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 320513 | 216272 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LG | NP81LG | np8 1lg | np81lg | Powys | Powys | Dan Y Parc Highways Depot STW | 1823 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 320794 | 215783 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LH | NP81LH | np8 1lh | np81lh | Powys | Powys | Dan Y Parc Highways Depot STW | 950 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 321742 | 216142 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LJ | NP81LJ | np8 1lj | np81lj | Powys | Powys | Dan Y Parc Highways Depot STW | 1420 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 320772 | 217342 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LL | NP81LL | np8 1ll | np81ll | Powys | Powys | Bwlch (S) STW | 1507 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 315556 | 218795 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LN | NP81LN | np8 1ln | np81ln | Powys | Powys | Bwlch (S) STW | 2381 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 314637 | 218082 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LP | NP81LP | np8 1lp | np81lp | Powys | Powys | Tretower STW | 1267 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 319081 | 219616 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LQ | NP81LQ | np8 1lq | np81lq | Powys | Powys | Dan Y Parc Highways Depot STW | 1206 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 321008 | 217385 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LR | NP81LR | np8 1lr | np81lr | Powys | Powys | Bwlch (S) STW | 1217 | 1161 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.64 | 11.54 | 12.76 | 316566 | 219714 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LS | NP81LS | np8 1ls | np81ls | Powys | Powys | Bwlch (S) STW | 593 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 315214 | 219781 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LT | NP81LT | np8 1lt | np81lt | Powys | Powys | Bwlch (S) STW | 450 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 315369 | 219870 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LU | NP81LU | np8 1lu | np81lu | Powys | Powys | Bwlch (S) STW | 398 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 315236 | 220002 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LW | NP81LW | np8 1lw | np81lw | Powys | Powys | Crickhowell STW | 2315 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 320588 | 218768 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LX | NP81LX | np8 1lx | np81lx | Powys | Powys | Bwlch (S) STW | 540 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 315134 | 219903 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LY | NP81LY | np8 1ly | np81ly | Powys | Powys | Bwlch (S) STW | 437 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 315300 | 219912 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1LZ | NP81LZ | np8 1lz | np81lz | Powys | Powys | Dan Y Parc Highways Depot STW | 1443 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 320739 | 217302 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NA | NP81NA | np8 1na | np81na | Powys | Powys | Bwlch (S) STW | 506 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 315024 | 220130 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NB | NP81NB | np8 1nb | np81nb | Powys | Powys | Bwlch (S) STW | 494 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 315062 | 220072 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1ND | NP81ND | np8 1nd | np81nd | Powys | Powys | Bwlch (S) STW | 1125 | 1281 | 1200to1500 | 2.56 | 1.88 | 1.38 | 23.88 | 12.73 | 14.07 | 314463 | 219865 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NE | NP81NE | np8 1ne | np81ne | Powys | Powys | Bwlch (S) STW | 655 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 314949 | 219946 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NF | NP81NF | np8 1nf | np81nf | Powys | Powys | Bwlch (S) STW | 935 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 314699 | 219819 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NG | NP81NG | np8 1ng | np81ng | Powys | Powys | Bwlch (S) STW | 790 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 315020 | 219673 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NH | NP81NH | np8 1nh | np81nh | Powys | Powys | Bwlch (S) STW | 875 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 315652 | 219439 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NJ | NP81NJ | np8 1nj | np81nj | Powys | Powys | Bwlch (S) STW | 812 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 315632 | 219499 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NL | NP81NL | np8 1nl | np81nl | Powys | Powys | Bwlch (S) STW | 912 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 315693 | 219409 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NN | NP81NN | np8 1nn | np81nn | Powys | Powys | Bwlch (S) STW | 976 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 315537 | 219325 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NP | NP81NP | np8 1np | np81np | Powys | Powys | Bwlch (S) STW | 1098 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 315439 | 219204 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NQ | NP81NQ | np8 1nq | np81nq | Powys | Powys | Bwlch (S) STW | 373 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 315162 | 220143 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NR | NP81NR | np8 1nr | np81nr | Powys | Powys | Bwlch (S) STW | 997 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 315519 | 219303 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NS | NP81NS | np8 1ns | np81ns | Powys | Powys | Bwlch (S) STW | 1214 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 315291 | 219105 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NT | NP81NT | np8 1nt | np81nt | Powys | Powys | Bwlch (S) STW | 1031 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 315313 | 219286 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NU | NP81NU | np8 1nu | np81nu | Powys | Powys | Aber STW | 3774 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 312073 | 218015 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NW | NP81NW | np8 1nw | np81nw | Powys | Powys | Bwlch (S) STW | 1153 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 315377 | 219154 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NX | NP81NX | np8 1nx | np81nx | Powys | Powys | Bwlch (S) STW | 476 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 315038 | 220185 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NY | NP81NY | np8 1ny | np81ny | Powys | Powys | Bwlch (S) STW | 894 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 315373 | 219415 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1NZ | NP81NZ | np8 1nz | np81nz | Powys | Powys | Bwlch (S) STW | 777 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 315511 | 219523 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PA | NP81PA | np8 1pa | np81pa | Powys | Powys | Dan Y Parc Highways Depot STW | 1273 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321152 | 217790 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PB | NP81PB | np8 1pb | np81pb | Powys | Powys | Dan Y Parc Highways Depot STW | 1302 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321075 | 217733 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PD | NP81PD | np8 1pd | np81pd | Powys | Powys | Dan Y Parc Highways Depot STW | 1314 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321044 | 217708 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PE | NP81PE | np8 1pe | np81pe | Powys | Powys | Dan Y Parc Highways Depot STW | 1366 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321000 | 217736 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PF | NP81PF | np8 1pf | np81pf | Powys | Powys | Dan Y Parc Highways Depot STW | 1332 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321031 | 217721 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PG | NP81PG | np8 1pg | np81pg | Powys | Powys | Dan Y Parc Highways Depot STW | 1355 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321046 | 217785 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PH | NP81PH | np8 1ph | np81ph | Powys | Powys | Dan Y Parc Highways Depot STW | 1371 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321039 | 217802 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PJ | NP81PJ | np8 1pj | np81pj | Powys | Powys | Dan Y Parc Highways Depot STW | 1399 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321052 | 217867 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PL | NP81PL | np8 1pl | np81pl | Powys | Powys | Dan Y Parc Highways Depot STW | 1148 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321125 | 217517 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PN | NP81PN | np8 1pn | np81pn | Powys | Powys | Dan Y Parc Highways Depot STW | 1150 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321173 | 217605 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PP | NP81PP | np8 1pp | np81pp | Powys | Powys | Dan Y Parc Highways Depot STW | 1161 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 321207 | 217676 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PQ | NP81PQ | np8 1pq | np81pq | Powys | Powys | Dan Y Parc Highways Depot STW | 1433 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 320988 | 217837 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PR | NP81PR | np8 1pr | np81pr | Powys | Powys | Crickhowell STW | 2029 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 320737 | 218465 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PS | NP81PS | np8 1ps | np81ps | Powys | Powys | Dan Y Parc Highways Depot STW | 1976 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 320751 | 218394 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PT | NP81PT | np8 1pt | np81pt | Powys | Powys | Dan Y Parc Highways Depot STW | 2024 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 320719 | 218431 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PU | NP81PU | np8 1pu | np81pu | Powys | Powys | Dan Y Parc Highways Depot STW | 2016 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 320654 | 218351 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PW | NP81PW | np8 1pw | np81pw | Powys | Powys | Tretower STW | 1780 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 317806 | 219466 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PX | NP81PX | np8 1px | np81px | Powys | Powys | Bwlch (S) STW | 1771 | 1259 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.47 | 12.52 | 13.83 | 317007 | 219370 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PY | NP81PY | np8 1py | np81py | Powys | Powys | Dan Y Parc Highways Depot STW | 2437 | 1250 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.3 | 12.43 | 13.73 | 320031 | 218202 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1PZ | NP81PZ | np8 1pz | np81pz | Powys | Powys | Bwlch (S) STW | 3010 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 317303 | 217891 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1QA | NP81QA | np8 1qa | np81qa | Powys | Powys | Dan Y Parc Highways Depot STW | 1254 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 320910 | 217183 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RB | NP81RB | np8 1rb | np81rb | Powys | Powys | Tretower STW | 2074 | 1105 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.6 | 10.98 | 12.14 | 320701 | 219842 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RD | NP81RD | np8 1rd | np81rd | Powys | Powys | Tretower STW | 534 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 318669 | 221351 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RE | NP81RE | np8 1re | np81re | Powys | Powys | Tretower STW | 759 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 318540 | 221538 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RF | NP81RF | np8 1rf | np81rf | Powys | Powys | Tretower STW | 603 | 1133 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.12 | 11.26 | 12.45 | 318495 | 221316 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RG | NP81RG | np8 1rg | np81rg | Powys | Powys | Tretower STW | 951 | 1126 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.99 | 11.19 | 12.37 | 319801 | 221172 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RH | NP81RH | np8 1rh | np81rh | Powys | Powys | Bwlch (S) STW | 1609 | 1161 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.64 | 11.54 | 12.76 | 317059 | 219904 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RJ | NP81RJ | np8 1rj | np81rj | Powys | Powys | Tretower STW | 459 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 318680 | 221273 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RL | NP81RL | np8 1rl | np81rl | Powys | Powys | Bwlch (S) STW | 1465 | 1161 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.64 | 11.54 | 12.76 | 316962 | 220206 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RN | NP81RN | np8 1rn | np81rn | Powys | Powys | Tretower STW | 1013 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 318372 | 220006 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RP | NP81RP | np8 1rp | np81rp | Powys | Powys | Cwmdu STW | 439 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 318046 | 223693 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RR | NP81RR | np8 1rr | np81rr | Powys | Powys | Cwmdu STW | 129 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 317875 | 223173 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RS | NP81RS | np8 1rs | np81rs | Powys | Powys | Cwmdu STW | 1239 | 1116 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.8 | 11.09 | 12.26 | 316678 | 223702 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RT | NP81RT | np8 1rt | np81rt | Powys | Powys | Cwmdu STW | 2288 | 1127 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.01 | 11.2 | 12.38 | 318201 | 225560 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RU | NP81RU | np8 1ru | np81ru | Powys | Powys | Cwmdu STW | 413 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 318122 | 223611 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RW | NP81RW | np8 1rw | np81rw | Powys | Powys | Cwmdu STW | 449 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 317970 | 223733 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1RY | NP81RY | np8 1ry | np81ry | Powys | Powys | Cwmdu STW | 54 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 317843 | 223354 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SA | NP81SA | np8 1sa | np81sa | Powys | Powys | Cwmdu STW | 50 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 317811 | 223269 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SB | NP81SB | np8 1sb | np81sb | Powys | Powys | Cwmdu STW | 1832 | 1134 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.14 | 11.27 | 12.46 | 316934 | 221714 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SE | NP81SE | np8 1se | np81se | Powys | Powys | Crickhowell STW | 1991 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 321562 | 219225 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SF | NP81SF | np8 1sf | np81sf | Powys | Powys | Tretower STW | 2014 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 320442 | 219575 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SG | NP81SG | np8 1sg | np81sg | Powys | Powys | Tretower STW | 1125 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 319697 | 220076 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SH | NP81SH | np8 1sh | np81sh | Powys | Powys | Tretower STW | 859 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 319228 | 220076 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SJ | NP81SJ | np8 1sj | np81sj | Powys | Powys | Llanbedr WwTW | 212 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 323805 | 220277 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SL | NP81SL | np8 1sl | np81sl | Powys | Powys | Crickhowell STW | 1009 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 322097 | 218395 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SN | NP81SN | np8 1sn | np81sn | Powys | Powys | Crickhowell STW | 883 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 322316 | 218335 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SP | NP81SP | np8 1sp | np81sp | Powys | Powys | Llanbedr WwTW | 1539 | 1129 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.04 | 11.22 | 12.4 | 322338 | 219648 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SQ | NP81SQ | np8 1sq | np81sq | Powys | Powys | Llanbedr WwTW | 207 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 323936 | 220237 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SR | NP81SR | np8 1sr | np81sr | Powys | Powys | Llanbedr WwTW | 320 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 323904 | 220374 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SS | NP81SS | np8 1ss | np81ss | Powys | Powys | Llanbedr WwTW | 311 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 323943 | 219781 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1ST | NP81ST | np8 1st | np81st | Powys | Powys | Llanbedr WwTW | 1665 | 1129 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.04 | 11.22 | 12.4 | 325483 | 220100 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SU | NP81SU | np8 1su | np81su | Powys | Powys | Llanbedr WwTW | 2628 | 1152 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.47 | 11.45 | 12.66 | 326417 | 220455 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SW | NP81SW | np8 1sw | np81sw | Powys | Powys | Crickhowell STW | 1416 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 322214 | 218858 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1SY | NP81SY | np8 1sy | np81sy | Powys | Powys | Llanbedr WwTW | 2272 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 323584 | 222325 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1TA | NP81TA | np8 1ta | np81ta | Powys | Powys | Llanbedr WwTW | 712 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 324413 | 220459 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1TB | NP81TB | np8 1tb | np81tb | Powys | Powys | Llanbedr WwTW | 587 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 323704 | 219491 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1TD | NP81TD | np8 1td | np81td | Powys | Powys | Llangenny STW | 1178 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 323059 | 218556 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1TE | NP81TE | np8 1te | np81te | Powys | Powys | Crickhowell STW | 759 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 323189 | 217142 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1TJ | NP81TJ | np8 1tj | np81tj | Powys | Powys | Glangrwyney STW | 555 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 323707 | 216592 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1TL | NP81TL | np8 1tl | np81tl | Powys | Powys | Crickhowell STW | 896 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 323354 | 217186 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1TN | NP81TN | np8 1tn | np81tn | Powys | Powys | Glangrwyney STW | 598 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 323620 | 216556 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP8 1TP | NP81TP | np8 1tp | np81tp | Powys | Powys | Crickhowell STW | 784 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 323262 | 217267 | Brecon Beacons National Park LPA | PO | River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
GL16 8PB | GL168PB | gl16 8pb | gl168pb | Monmouthshire | Sir Fynwy | Monmouth STW | 1896 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 353334 | 212382 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
HR3 5AA | HR35AA | hr3 5aa | hr35aa | Powys | Powys | Clyro WwTW | 1908 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322981 | 242421 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AB | HR35AB | hr3 5ab | hr35ab | Powys | Powys | Clyro WwTW | 1991 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323090 | 242410 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AD | HR35AD | hr3 5ad | hr35ad | Powys | Powys | Clyro WwTW | 2107 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323171 | 242327 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AE | HR35AE | hr3 5ae | hr35ae | Powys | Powys | Clyro WwTW | 1916 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322961 | 242392 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AF | HR35AF | hr3 5af | hr35af | Powys | Powys | Clyro WwTW | 1948 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322974 | 242362 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AG | HR35AG | hr3 5ag | hr35ag | Powys | Powys | Clyro WwTW | 1974 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323023 | 242370 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AH | HR35AH | hr3 5ah | hr35ah | Powys | Powys | Clyro WwTW | 2021 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323003 | 242290 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AJ | HR35AJ | hr3 5aj | hr35aj | Powys | Powys | Clyro WwTW | 2059 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323023 | 242258 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AN | HR35AN | hr3 5an | hr35an | Powys | Powys | Clyro WwTW | 2032 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323092 | 242355 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AP | HR35AP | hr3 5ap | hr35ap | Powys | Powys | Clyro WwTW | 2209 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323248 | 242259 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AQ | HR35AQ | hr3 5aq | hr35aq | Powys | Powys | Clyro WwTW | 1995 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323018 | 242338 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AR | HR35AR | hr3 5ar | hr35ar | Powys | Powys | Clyro WwTW | 2070 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323200 | 242408 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AS | HR35AS | hr3 5as | hr35as | Powys | Powys | Clyro WwTW | 1994 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323130 | 242445 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AT | HR35AT | hr3 5at | hr35at | Powys | Powys | Clyro WwTW | 1845 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 323033 | 242559 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AU | HR35AU | hr3 5au | hr35au | Powys | Powys | Clyro WwTW | 1845 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 323041 | 242568 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AW | HR35AW | hr3 5aw | hr35aw | Powys | Powys | Clyro WwTW | 2198 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323203 | 242231 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AX | HR35AX | hr3 5ax | hr35ax | Powys | Powys | Clyro WwTW | 1823 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 323018 | 242576 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AY | HR35AY | hr3 5ay | hr35ay | Powys | Powys | Clyro WwTW | 1874 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 323041 | 242526 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5AZ | HR35AZ | hr3 5az | hr35az | Powys | Powys | Clyro WwTW | 1926 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 323090 | 242502 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BA | HR35BA | hr3 5ba | hr35ba | Powys | Powys | Clyro WwTW | 1751 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 323061 | 242733 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BG | HR35BG | hr3 5bg | hr35bg | Powys | Powys | Clyro WwTW | 1739 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 322991 | 242670 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BH | HR35BH | hr3 5bh | hr35bh | Powys | Powys | Clyro WwTW | 1860 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 323085 | 242593 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BJ | HR35BJ | hr3 5bj | hr35bj | Powys | Powys | Clyro WwTW | 1728 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 323000 | 242696 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BL | HR35BL | hr3 5bl | hr35bl | Powys | Powys | Clyro WwTW | 1910 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323019 | 242453 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BN | HR35BN | hr3 5bn | hr35bn | Powys | Powys | Clyro WwTW | 1953 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323019 | 242395 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BP | HR35BP | hr3 5bp | hr35bp | Powys | Powys | Clyro WwTW | 1946 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323089 | 242472 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BQ | HR35BQ | hr3 5bq | hr35bq | Powys | Powys | Clyro WwTW | 1893 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323028 | 242486 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BS | HR35BS | hr3 5bs | hr35bs | Powys | Powys | Clyro WwTW | 1823 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322799 | 242381 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BT | HR35BT | hr3 5bt | hr35bt | Powys | Powys | Clyro WwTW | 2081 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322900 | 242135 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BU | HR35BU | hr3 5bu | hr35bu | Powys | Powys | Clyro WwTW | 1886 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322929 | 242405 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BW | HR35BW | hr3 5bw | hr35bw | Powys | Powys | Clyro WwTW | 2095 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323139 | 242313 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5BY | HR35BY | hr3 5by | hr35by | Powys | Powys | Clyro WwTW | 1866 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322996 | 242492 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DA | HR35DA | hr3 5da | hr35da | Powys | Powys | Clyro WwTW | 1837 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322849 | 242402 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DB | HR35DB | hr3 5db | hr35db | Powys | Powys | Clyro WwTW | 1798 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 322925 | 242519 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DD | HR35DD | hr3 5dd | hr35dd | Powys | Powys | Clyro WwTW | 1839 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322930 | 242468 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DE | HR35DE | hr3 5de | hr35de | Powys | Powys | Clyro WwTW | 1760 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 322901 | 242548 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DF | HR35DF | hr3 5df | hr35df | Powys | Powys | Clyro WwTW | 1897 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322832 | 242313 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DG | HR35DG | hr3 5dg | hr35dg | Powys | Powys | Clyro WwTW | 1954 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322850 | 242256 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DH | HR35DH | hr3 5dh | hr35dh | Powys | Powys | Clyro WwTW | 1747 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 322942 | 242606 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DJ | HR35DJ | hr3 5dj | hr35dj | Powys | Powys | Clyro WwTW | 1834 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322945 | 242488 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DL | HR35DL | hr3 5dl | hr35dl | Powys | Powys | Clyro WwTW | 2007 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322769 | 242137 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DN | HR35DN | hr3 5dn | hr35dn | Powys | Powys | Clyro WwTW | 2009 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322694 | 242090 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DP | HR35DP | hr3 5dp | hr35dp | Powys | Powys | Clyro WwTW | 1978 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322727 | 242145 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DQ | HR35DQ | hr3 5dq | hr35dq | Powys | Powys | Clyro WwTW | 1925 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322730 | 242209 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DR | HR35DR | hr3 5dr | hr35dr | Powys | Powys | Clyro WwTW | 1806 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 322450 | 242193 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DS | HR35DS | hr3 5ds | hr35ds | Powys | Powys | Clyro WwTW | 2204 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322942 | 242015 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DT | HR35DT | hr3 5dt | hr35dt | Powys | Powys | Clyro WwTW | 2063 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322768 | 242071 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DU | HR35DU | hr3 5du | hr35du | Powys | Powys | Clyro WwTW | 2166 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322795 | 241967 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DW | HR35DW | hr3 5dw | hr35dw | Powys | Powys | Clyro WwTW | 2004 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322717 | 242109 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DX | HR35DX | hr3 5dx | hr35dx | Powys | Powys | Clyro WwTW | 2123 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322793 | 242015 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DY | HR35DY | hr3 5dy | hr35dy | Powys | Powys | Clyro WwTW | 2084 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322625 | 241968 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5DZ | HR35DZ | hr3 5dz | hr35dz | Powys | Powys | Clyro WwTW | 2061 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322580 | 241972 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5EA | HR35EA | hr3 5ea | hr35ea | Powys | Powys | Clyro WwTW | 1993 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322619 | 242067 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5EB | HR35EB | hr3 5eb | hr35eb | Powys | Powys | Clyro WwTW | 1995 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322592 | 242051 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5ED | HR35ED | hr3 5ed | hr35ed | Powys | Powys | Clyro WwTW | 1957 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322602 | 242099 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5EE | HR35EE | hr3 5ee | hr35ee | Powys | Powys | Clyro WwTW | 1951 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322568 | 242088 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5EF | HR35EF | hr3 5ef | hr35ef | Powys | Powys | Clyro WwTW | 1895 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322523 | 242129 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5EG | HR35EG | hr3 5eg | hr35eg | Powys | Powys | Clyro WwTW | 1936 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 322422 | 242040 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5EH | HR35EH | hr3 5eh | hr35eh | Powys | Powys | Clyro WwTW | 2264 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323016 | 241993 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5EJ | HR35EJ | hr3 5ej | hr35ej | Powys | Powys | Clyro WwTW | 2246 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322921 | 241950 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5EL | HR35EL | hr3 5el | hr35el | Powys | Powys | Clyro WwTW | 1823 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 322208 | 242085 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5EQ | HR35EQ | hr3 5eq | hr35eq | Powys | Powys | Clyro WwTW | 1943 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322874 | 242287 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5FA | HR35FA | hr3 5fa | hr35fa | Powys | Powys | Clyro WwTW | 2428 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323047 | 241815 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5FB | HR35FB | hr3 5fb | hr35fb | Powys | Powys | Clyro WwTW | 443 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321399 | 243513 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5FD | HR35FD | hr3 5fd | hr35fd | Powys | Powys | Clyro WwTW | 1937 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322963 | 242366 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5FG | HR35FG | hr3 5fg | hr35fg | Powys | Powys | Llanigon WwTW | 5032 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 325275 | 239012 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5HZ | HR35HZ | hr3 5hz | hr35hz | Powys | Powys | Clyro WwTW | 285 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321433 | 243742 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JA | HR35JA | hr3 5ja | hr35ja | Powys | Powys | Llowes STW | 174 | 885 | 700to900 | 1.77 | 1.3 | 0.95 | 16.5 | 8.8 | 9.72 | 319244 | 241676 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JB | HR35JB | hr3 5jb | hr35jb | Powys | Powys | Llowes STW | 264 | 885 | 700to900 | 1.77 | 1.3 | 0.95 | 16.5 | 8.8 | 9.72 | 319196 | 241767 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JD | HR35JD | hr3 5jd | hr35jd | Powys | Powys | Llowes STW | 383 | 885 | 700to900 | 1.77 | 1.3 | 0.95 | 16.5 | 8.8 | 9.72 | 319054 | 241763 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JE | HR35JE | hr3 5je | hr35je | Powys | Powys | Llowes STW | 1014 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 318386 | 241583 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JF | HR35JF | hr3 5jf | hr35jf | Powys | Powys | Llowes STW | 1960 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 317539 | 242212 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JG | HR35JG | hr3 5jg | hr35jg | Powys | Powys | Painscastle STW | 2755 | 1013 | 900to1200 | 2.03 | 1.48 | 1.09 | 18.88 | 10.07 | 11.13 | 317184 | 243547 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JH | HR35JH | hr3 5jh | hr35jh | Powys | Powys | Painscastle STW | 2621 | 971 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.1 | 9.65 | 10.67 | 318750 | 244264 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JJ | HR35JJ | hr3 5jj | hr35jj | Powys | Powys | Clyro WwTW | 2566 | 971 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.1 | 9.65 | 10.67 | 319168 | 244237 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JL | HR35JL | hr3 5jl | hr35jl | Powys | Powys | Painscastle STW | 2214 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 319089 | 245329 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JP | HR35JP | hr3 5jp | hr35jp | Powys | Powys | Llowes STW | 2077 | 971 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.1 | 9.65 | 10.67 | 319014 | 243640 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JR | HR35JR | hr3 5jr | hr35jr | Powys | Powys | Llowes STW | 1823 | 902 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.81 | 8.97 | 9.91 | 319824 | 243372 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JS | HR35JS | hr3 5js | hr35js | Powys | Powys | Llowes STW | 1255 | 927 | 900to1200 | 1.86 | 1.36 | 1 | 17.28 | 9.21 | 10.18 | 318850 | 242728 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JT | HR35JT | hr3 5jt | hr35jt | Powys | Powys | Llowes STW | 1613 | 902 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.81 | 8.97 | 9.91 | 320149 | 243028 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JU | HR35JU | hr3 5ju | hr35ju | Powys | Powys | Llowes STW | 1557 | 902 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.81 | 8.97 | 9.91 | 319992 | 243040 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JW | HR35JW | hr3 5jw | hr35jw | Powys | Powys | Clyro WwTW | 2277 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 319520 | 244484 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JX | HR35JX | hr3 5jx | hr35jx | Powys | Powys | Llowes STW | 1253 | 927 | 900to1200 | 1.86 | 1.36 | 1 | 17.28 | 9.21 | 10.18 | 319406 | 242853 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JY | HR35JY | hr3 5jy | hr35jy | Powys | Powys | Glasbury STW | 610 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 318100 | 238962 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5JZ | HR35JZ | hr3 5jz | hr35jz | Powys | Powys | Clyro WwTW | 204 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 321520 | 243743 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LA | HR35LA | hr3 5la | hr35la | Powys | Powys | Clyro WwTW | 997 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 322221 | 242985 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LB | HR35LB | hr3 5lb | hr35lb | Powys | Powys | Clyro WwTW | 609 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321145 | 243590 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LD | HR35LD | hr3 5ld | hr35ld | Powys | Powys | Clyro WwTW | 765 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 321044 | 243446 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LE | HR35LE | hr3 5le | hr35le | Powys | Powys | Clyro WwTW | 860 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 321180 | 243153 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LF | HR35LF | hr3 5lf | hr35lf | Powys | Powys | Clyro WwTW | 1924 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 322107 | 241956 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5LG | HR35LG | hr3 5lg | hr35lg | Powys | Powys | Llowes STW | 1235 | 897 | 700to900 | 1.8 | 1.31 | 0.96 | 16.72 | 8.92 | 9.86 | 318323 | 240997 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LH | HR35LH | hr3 5lh | hr35lh | Powys | Powys | Glasbury STW | 420 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 317619 | 239274 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LJ | HR35LJ | hr3 5lj | hr35lj | Powys | Powys | Glasbury STW | 486 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 317653 | 239154 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LL | HR35LL | hr3 5ll | hr35ll | Powys | Powys | Glasbury STW | 512 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 317640 | 239131 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LN | HR35LN | hr3 5ln | hr35ln | Powys | Powys | Glasbury STW | 517 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 317538 | 239220 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LP | HR35LP | hr3 5lp | hr35lp | Powys | Powys | Glasbury STW | 722 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 317222 | 239441 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LQ | HR35LQ | hr3 5lq | hr35lq | Powys | Powys | Glasbury STW | 987 | 874 | 700to900 | 1.75 | 1.28 | 0.94 | 16.29 | 8.69 | 9.6 | 317338 | 240334 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LR | HR35LR | hr3 5lr | hr35lr | Powys | Powys | Glasbury STW | 1181 | 874 | 700to900 | 1.75 | 1.28 | 0.94 | 16.29 | 8.69 | 9.6 | 316758 | 239634 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LS | HR35LS | hr3 5ls | hr35ls | Powys | Powys | Glasbury STW | 1185 | 874 | 700to900 | 1.75 | 1.28 | 0.94 | 16.29 | 8.69 | 9.6 | 316756 | 239654 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LT | HR35LT | hr3 5lt | hr35lt | Powys | Powys | Glasbury STW | 1145 | 874 | 700to900 | 1.75 | 1.28 | 0.94 | 16.29 | 8.69 | 9.6 | 316795 | 239639 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LU | HR35LU | hr3 5lu | hr35lu | Powys | Powys | Glasbury STW | 2039 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 316240 | 240680 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LW | HR35LW | hr3 5lw | hr35lw | Powys | Powys | Glasbury STW | 549 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 317442 | 239309 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LX | HR35LX | hr3 5lx | hr35lx | Powys | Powys | Glasbury STW | 2315 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 316366 | 241249 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LY | HR35LY | hr3 5ly | hr35ly | Powys | Powys | Glasbury STW | 2043 | 918 | 900to1200 | 1.84 | 1.34 | 0.99 | 17.11 | 9.13 | 10.09 | 316896 | 241307 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5LZ | HR35LZ | hr3 5lz | hr35lz | Powys | Powys | Glasbury STW | 2446 | 946 | 900to1200 | 1.89 | 1.39 | 1.02 | 17.63 | 9.4 | 10.39 | 316940 | 241782 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NA | HR35NA | hr3 5na | hr35na | Powys | Powys | Llowes STW | 3134 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 316554 | 242910 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NB | HR35NB | hr3 5nb | hr35nb | Powys | Powys | Llyswen STW | 3908 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 314674 | 241834 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5ND | HR35ND | hr3 5nd | hr35nd | Powys | Powys | Glasbury STW | 2856 | 943 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.58 | 9.37 | 10.36 | 316047 | 241690 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NE | HR35NE | hr3 5ne | hr35ne | Powys | Powys | Glasbury STW | 2322 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 316440 | 241324 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NF | HR35NF | hr3 5nf | hr35nf | Powys | Powys | Glasbury STW | 523 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 317556 | 239190 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NG | HR35NG | hr3 5ng | hr35ng | Powys | Powys | Erwood STW | 4169 | 992 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.49 | 9.86 | 10.9 | 314164 | 243119 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NH | HR35NH | hr3 5nh | hr35nh | Powys | Powys | Glasbury STW | 532 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 318074 | 239035 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NJ | HR35NJ | hr3 5nj | hr35nj | Powys | Powys | Glasbury STW | 1319 | 897 | 700to900 | 1.8 | 1.31 | 0.96 | 16.72 | 8.92 | 9.86 | 317724 | 240850 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NL | HR35NL | hr3 5nl | hr35nl | Powys | Powys | Glasbury STW | 161 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 317776 | 239562 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NN | HR35NN | hr3 5nn | hr35nn | Powys | Powys | Glasbury STW | 337 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 317688 | 239321 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NP | HR35NP | hr3 5np | hr35np | Powys | Powys | Glasbury STW | 287 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 318061 | 239291 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NQ | HR35NQ | hr3 5nq | hr35nq | Powys | Powys | Clyro WwTW | 243 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321487 | 243724 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NR | HR35NR | hr3 5nr | hr35nr | Powys | Powys | Glasbury STW | 325 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 318168 | 239321 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NS | HR35NS | hr3 5ns | hr35ns | Powys | Powys | Glasbury STW | 374 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 318278 | 239399 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NT | HR35NT | hr3 5nt | hr35nt | Powys | Powys | Glasbury STW | 916 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 317752 | 238652 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NU | HR35NU | hr3 5nu | hr35nu | Powys | Powys | Aberllynfi Three Cocks | 861 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 317829 | 238546 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NW | HR35NW | hr3 5nw | hr35nw | Powys | Powys | Glasbury STW | 372 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 317766 | 239218 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NX | HR35NX | hr3 5nx | hr35nx | Powys | Powys | Glasbury STW | 904 | 874 | 700to900 | 1.75 | 1.28 | 0.94 | 16.29 | 8.69 | 9.6 | 318695 | 239058 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NY | HR35NY | hr3 5ny | hr35ny | Powys | Powys | Llanigon WwTW | 714 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 320026 | 239932 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5NZ | HR35NZ | hr3 5nz | hr35nz | Powys | Powys | Glasbury STW | 1938 | 890 | 700to900 | 1.78 | 1.3 | 0.96 | 16.59 | 8.85 | 9.78 | 316087 | 240129 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PA | HR35PA | hr3 5pa | hr35pa | Powys | Powys | Glasbury STW | 1609 | 862 | 700to900 | 1.73 | 1.26 | 0.93 | 16.07 | 8.57 | 9.47 | 316384 | 239128 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PB | HR35PB | hr3 5pb | hr35pb | Powys | Powys | Aberllynfi Three Cocks | 1079 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 316580 | 238501 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PD | HR35PD | hr3 5pd | hr35pd | Powys | Powys | Glasbury STW | 556 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 318130 | 239028 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PE | HR35PE | hr3 5pe | hr35pe | Powys | Powys | Glasbury STW | 636 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 318187 | 238965 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PF | HR35PF | hr3 5pf | hr35pf | Powys | Powys | Glasbury STW | 582 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 318181 | 239021 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PG | HR35PG | hr3 5pg | hr35pg | Powys | Powys | Clyro WwTW | 2031 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 322141 | 241854 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5PH | HR35PH | hr3 5ph | hr35ph | Powys | Powys | Clyro WwTW | 2066 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 322433 | 241904 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5PJ | HR35PJ | hr3 5pj | hr35pj | Powys | Powys | Clyro WwTW | 2080 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 322322 | 241851 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5PL | HR35PL | hr3 5pl | hr35pl | Powys | Powys | Llanigon WwTW | 1821 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 321981 | 241505 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5PN | HR35PN | hr3 5pn | hr35pn | Powys | Powys | Llanigon WwTW | 1153 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 321501 | 241004 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PP | HR35PP | hr3 5pp | hr35pp | Powys | Powys | Llanigon WwTW | 1193 | 862 | 700to900 | 1.73 | 1.26 | 0.93 | 16.07 | 8.57 | 9.47 | 321253 | 241391 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PQ | HR35PQ | hr3 5pq | hr35pq | Powys | Powys | Llanigon WwTW | 816 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 321247 | 240252 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5PR | HR35PR | hr3 5pr | hr35pr | Powys | Powys | Llanigon WwTW | 149 | 855 | 700to900 | 1.71 | 1.25 | 0.92 | 15.94 | 8.5 | 9.39 | 320342 | 240573 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PS | HR35PS | hr3 5ps | hr35ps | Powys | Powys | Llanigon WwTW | 714 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 320026 | 239932 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PT | HR35PT | hr3 5pt | hr35pt | Powys | Powys | Glasbury STW | 1241 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 319156 | 239774 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PU | HR35PU | hr3 5pu | hr35pu | Powys | Powys | Llanigon WwTW | 397 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 320845 | 240368 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PW | HR35PW | hr3 5pw | hr35pw | Powys | Powys | Clyro WwTW | 1918 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 321889 | 241928 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5PX | HR35PX | hr3 5px | hr35px | Powys | Powys | Llanigon WwTW | 1687 | 924 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.22 | 9.19 | 10.15 | 322009 | 239808 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5PY | HR35PY | hr3 5py | hr35py | Powys | Powys | Llanigon WwTW | 2716 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 322900 | 239285 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5PZ | HR35PZ | hr3 5pz | hr35pz | Powys | Powys | Llanigon WwTW | 904 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 321320 | 240193 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QA | HR35QA | hr3 5qa | hr35qa | Powys | Powys | Llanigon WwTW | 1093 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 321364 | 239868 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QB | HR35QB | hr3 5qb | hr35qb | Powys | Powys | Llanigon WwTW | 1290 | 895 | 700to900 | 1.79 | 1.31 | 0.96 | 16.68 | 8.9 | 9.83 | 321281 | 239492 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QD | HR35QD | hr3 5qd | hr35qd | Powys | Powys | Fforddlas STW | 2080 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 322099 | 238089 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QE | HR35QE | hr3 5qe | hr35qe | Powys | Powys | Fforddlas STW | 729 | 895 | 700to900 | 1.79 | 1.31 | 0.96 | 16.68 | 8.9 | 9.83 | 320733 | 239060 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QF | HR35QF | hr3 5qf | hr35qf | Powys | Powys | Fforddlas STW | 436 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 320448 | 238958 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QG | HR35QG | hr3 5qg | hr35qg | Powys | Powys | Fforddlas STW | 329 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 319804 | 238816 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5QH | HR35QH | hr3 5qh | hr35qh | Powys | Powys | Fforddlas STW | 1156 | 956 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.82 | 9.5 | 10.5 | 320940 | 237886 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QJ | HR35QJ | hr3 5qj | hr35qj | Powys | Powys | Fforddlas STW | 3046 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 322045 | 236338 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QL | HR35QL | hr3 5ql | hr35ql | Powys | Powys | Fforddlas STW | 2081 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 321614 | 237253 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QN | HR35QN | hr3 5qn | hr35qn | Powys | Powys | Fforddlas STW | 1362 | 956 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.82 | 9.5 | 10.5 | 321385 | 238216 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QP | HR35QP | hr3 5qp | hr35qp | Powys | Powys | Fforddlas STW | 2714 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 322797 | 239040 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QQ | HR35QQ | hr3 5qq | hr35qq | Powys | Powys | Fforddlas STW | 244 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 320252 | 238491 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QR | HR35QR | hr3 5qr | hr35qr | Powys | Powys | Clyro WwTW | 1951 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 322308 | 241982 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QS | HR35QS | hr3 5qs | hr35qs | Powys | Powys | Clyro WwTW | 1927 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 322224 | 241982 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QT | HR35QT | hr3 5qt | hr35qt | Powys | Powys | Llanigon WwTW | 849 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 321289 | 240277 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QU | HR35QU | hr3 5qu | hr35qu | Powys | Powys | Llanigon WwTW | 938 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 321367 | 240226 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5QW | HR35QW | hr3 5qw | hr35qw | Powys | Powys | Fforddlas STW | 1896 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 321995 | 238856 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5RE | HR35RE | hr3 5re | hr35re | Powys | Powys | Clyro WwTW | 2666 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 323408 | 241789 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5RH | HR35RH | hr3 5rh | hr35rh | Powys | Powys | Llanigon WwTW | 2755 | 972 | 900to1200 | 1.95 | 1.42 | 1.04 | 18.12 | 9.66 | 10.68 | 323103 | 239691 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5RJ | HR35RJ | hr3 5rj | hr35rj | Powys | Powys | Fforddlas STW | 3961 | 1237 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.06 | 12.3 | 13.59 | 323338 | 236398 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5RL | HR35RL | hr3 5rl | hr35rl | Powys | Powys | Llanigon WwTW | 3155 | 998 | 900to1200 | 2 | 1.46 | 1.07 | 18.6 | 9.92 | 10.96 | 323610 | 240214 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5RP | HR35RP | hr3 5rp | hr35rp | Powys | Powys | Llanigon WwTW | 795 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 321211 | 240211 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5RR | HR35RR | hr3 5rr | hr35rr | Powys | Powys | Clyro WwTW | 215 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321496 | 243896 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5RS | HR35RS | hr3 5rs | hr35rs | Powys | Powys | Clyro WwTW | 1112 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 322547 | 243113 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5RT | HR35RT | hr3 5rt | hr35rt | Powys | Powys | Clyro WwTW | 812 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 322496 | 243669 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5RU | HR35RU | hr3 5ru | hr35ru | Powys | Powys | Clyro WwTW | 677 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 322078 | 244399 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5RX | HR35RX | hr3 5rx | hr35rx | Powys | Powys | Clyro WwTW | 1605 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322624 | 245149 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5RY | HR35RY | hr3 5ry | hr35ry | Powys | Powys | Clyro WwTW | 2724 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 323357 | 245998 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5RZ | HR35RZ | hr3 5rz | hr35rz | Powys | Powys | Clyro WwTW | 279 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321423 | 243841 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SA | HR35SA | hr3 5sa | hr35sa | Powys | Powys | Clyro WwTW | 301 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321402 | 243809 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SB | HR35SB | hr3 5sb | hr35sb | Powys | Powys | Clyro WwTW | 404 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321364 | 243615 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SD | HR35SD | hr3 5sd | hr35sd | Powys | Powys | Clyro WwTW | 448 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 321442 | 243471 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SE | HR35SE | hr3 5se | hr35se | Powys | Powys | Clyro WwTW | 573 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321135 | 243920 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SF | HR35SF | hr3 5sf | hr35sf | Powys | Powys | Clyro WwTW | 425 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321277 | 243850 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SG | HR35SG | hr3 5sg | hr35sg | Powys | Powys | Clyro WwTW | 1698 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 320049 | 244223 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SH | HR35SH | hr3 5sh | hr35sh | Powys | Powys | Painscastle STW | 3037 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 320062 | 246965 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SJ | HR35SJ | hr3 5sj | hr35sj | Powys | Powys | Clyro WwTW | 2858 | 977 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.21 | 9.71 | 10.73 | 320548 | 246450 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SL | HR35SL | hr3 5sl | hr35sl | Powys | Powys | Clyro WwTW | 1203 | 902 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.81 | 8.97 | 9.91 | 321757 | 245037 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SN | HR35SN | hr3 5sn | hr35sn | Powys | Powys | Clyro WwTW | 1466 | 927 | 900to1200 | 1.86 | 1.36 | 1 | 17.28 | 9.21 | 10.18 | 321047 | 245147 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SP | HR35SP | hr3 5sp | hr35sp | Powys | Powys | Clyro WwTW | 313 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321434 | 243675 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SQ | HR35SQ | hr3 5sq | hr35sq | Powys | Powys | Painscastle STW | 2547 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 319596 | 245798 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SR | HR35SR | hr3 5sr | hr35sr | Powys | Powys | Clyro WwTW | 607 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321095 | 243837 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SS | HR35SS | hr3 5ss | hr35ss | Powys | Powys | Clyro WwTW | 347 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321363 | 243909 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SW | HR35SW | hr3 5sw | hr35sw | Powys | Powys | Clyro WwTW | 329 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 321513 | 244105 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5SZ | HR35SZ | hr3 5sz | hr35sz | Powys | Powys | Clyro WwTW | 245 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 321511 | 243682 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5TH | HR35TH | hr3 5th | hr35th | Powys | Powys | Glasbury STW | 345 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 317727 | 239275 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5TJ | HR35TJ | hr3 5tj | hr35tj | Powys | Powys | Glasbury STW | 589 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 317961 | 238961 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5TL | HR35TL | hr3 5tl | hr35tl | Powys | Powys | Clyro WwTW | 1823 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 321978 | 242035 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5TN | HR35TN | hr3 5tn | hr35tn | Powys | Powys | Clyro WwTW | 1793 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 322047 | 242077 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 5TP | HR35TP | hr3 5tp | hr35tp | Powys | Powys | Clyro WwTW | 240 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 321475 | 243914 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5TQ | HR35TQ | hr3 5tq | hr35tq | Powys | Powys | Llanigon WwTW | 857 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 321216 | 240075 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5TR | HR35TR | hr3 5tr | hr35tr | Powys | Powys | Clyro WwTW | 109 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 321811 | 243837 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 5ZZ | HR35ZZ | hr3 5zz | hr35zz | Powys | Powys | Clyro WwTW | 1928 | 870 | 700to900 | 1.74 | 1.27 | 0.93 | 16.22 | 8.65 | 9.56 | 322977 | 242391 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
HR3 6BW | HR36BW | hr3 6bw | hr36bw | Powys | Powys | Clyro WwTW | 5408 | 1042 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.42 | 10.36 | 11.45 | 321955 | 249236 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 6EX | HR36EX | hr3 6ex | hr36ex | Powys | Powys | Clyro WwTW | 2857 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 323555 | 246009 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 6EY | HR36EY | hr3 6ey | hr36ey | Powys | Powys | Clyro WwTW | 4177 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324026 | 247305 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 6HA | HR36HA | hr3 6ha | hr36ha | Powys | Powys | Clyro WwTW | 3593 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 322592 | 247316 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 6HL | HR36HL | hr3 6hl | hr36hl | Powys | Powys | Clyro WwTW | 4622 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 321679 | 248456 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 6HN | HR36HN | hr3 6hn | hr36hn | Powys | Powys | Painscastle STW | 3921 | 1044 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.46 | 10.38 | 11.47 | 320439 | 248354 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 6JJ | HR36JJ | hr3 6jj | hr36jj | Powys | Powys | Clyro WwTW | 7823 | 951 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.73 | 9.45 | 10.45 | 325736 | 250536 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 6JU | HR36JU | hr3 6ju | hr36ju | Powys | Powys | Clyro WwTW | 3098 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 321152 | 246884 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 6JW | HR36JW | hr3 6jw | hr36jw | Powys | Powys | Old Radnor STW | 8128 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 326749 | 251553 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 6JX | HR36JX | hr3 6jx | hr36jx | Powys | Powys | Clyro WwTW | 2652 | 977 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.21 | 9.71 | 10.73 | 321261 | 246450 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR3 6JY | HR36JY | hr3 6jy | hr36jy | Powys | Powys | Clyro WwTW | 2106 | 938 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.48 | 9.32 | 10.31 | 321716 | 245941 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3EP | HR53EP | hr5 3ep | hr53ep | Powys | Powys | Old Radnor STW | 4288 | 1029 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.18 | 10.23 | 11.31 | 324995 | 255128 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3ND | HR53ND | hr5 3nd | hr53nd | Powys | Powys | Old Radnor STW | 5994 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 323252 | 253571 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3NP | HR53NP | hr5 3np | hr53np | Powys | Powys | Old Radnor STW | 1724 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 326003 | 258345 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3NR | HR53NR | hr5 3nr | hr53nr | Powys | Powys | Old Radnor STW | 4539 | 1047 | 900to1200 | 2.1 | 1.53 | 1.12 | 19.51 | 10.41 | 11.5 | 323191 | 255100 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3NS | HR53NS | hr5 3ns | hr53ns | Powys | Powys | Old Radnor STW | 4089 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 322733 | 255784 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3NT | HR53NT | hr5 3nt | hr53nt | Powys | Powys | Old Radnor STW | 4877 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 321948 | 255335 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3NU | HR53NU | hr5 3nu | hr53nu | Powys | Powys | Old Radnor STW | 4683 | 1047 | 900to1200 | 2.1 | 1.53 | 1.12 | 19.51 | 10.41 | 11.5 | 323190 | 254949 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3NW | HR53NW | hr5 3nw | hr53nw | Powys | Powys | Old Radnor STW | 1968 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 326232 | 258244 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3NX | HR53NX | hr5 3nx | hr53nx | Powys | Powys | Old Radnor STW | 4878 | 1047 | 900to1200 | 2.1 | 1.53 | 1.12 | 19.51 | 10.41 | 11.5 | 323076 | 254781 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3NY | HR53NY | hr5 3ny | hr53ny | Powys | Powys | Old Radnor STW | 4554 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 323729 | 254940 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3NZ | HR53NZ | hr5 3nz | hr53nz | Powys | Powys | Old Radnor STW | 5394 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 324897 | 254014 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3PA | HR53PA | hr5 3pa | hr53pa | Powys | Powys | Old Radnor STW | 5483 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 324832 | 253922 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3PD | HR53PD | hr5 3pd | hr53pd | Powys | Powys | Old Radnor STW | 5272 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 324078 | 254160 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3PE | HR53PE | hr5 3pe | hr53pe | Powys | Powys | Old Radnor STW | 6247 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 323830 | 253208 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3PJ | HR53PJ | hr5 3pj | hr53pj | Powys | Powys | Old Radnor STW | 7177 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 323230 | 252365 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3PL | HR53PL | hr5 3pl | hr53pl | Powys | Powys | Old Radnor STW | 6482 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 322557 | 253264 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3PN | HR53PN | hr5 3pn | hr53pn | Powys | Powys | Old Radnor STW | 6465 | 1107 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.63 | 11 | 12.16 | 321905 | 253544 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3PP | HR53PP | hr5 3pp | hr53pp | Powys | Powys | Old Radnor STW | 3569 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 323361 | 256069 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3PR | HR53PR | hr5 3pr | hr53pr | Powys | Powys | Old Radnor STW | 4733 | 1047 | 900to1200 | 2.1 | 1.53 | 1.12 | 19.51 | 10.41 | 11.5 | 323130 | 254916 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3PW | HR53PW | hr5 3pw | hr53pw | Powys | Powys | Old Radnor STW | 5420 | 1107 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.63 | 11 | 12.16 | 322499 | 254423 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QB | HR53QB | hr5 3qb | hr53qb | Powys | Powys | Clyro WwTW | 8013 | 975 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.17 | 9.69 | 10.71 | 325211 | 251037 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QD | HR53QD | hr5 3qd | hr53qd | Powys | Powys | Clyro WwTW | 7336 | 975 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.17 | 9.69 | 10.71 | 324670 | 250542 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QE | HR53QE | hr5 3qe | hr53qe | Powys | Powys | Clyro WwTW | 7409 | 1008 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.79 | 10.02 | 11.07 | 324067 | 250855 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QF | HR53QF | hr5 3qf | hr53qf | Powys | Powys | Painscastle STW | 6337 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321665 | 250693 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QG | HR53QG | hr5 3qg | hr53qg | Powys | Powys | Painscastle STW | 4769 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 320586 | 249552 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QH | HR53QH | hr5 3qh | hr53qh | Powys | Powys | Painscastle STW | 4576 | 1060 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.76 | 10.54 | 11.65 | 319521 | 250181 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QJ | HR53QJ | hr5 3qj | hr53qj | Powys | Powys | Painscastle STW | 4080 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 319978 | 249190 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QL | HR53QL | hr5 3ql | hr53ql | Powys | Powys | Painscastle STW | 3596 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 318901 | 249411 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QN | HR53QN | hr5 3qn | hr53qn | Powys | Powys | Painscastle STW | 3606 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 318444 | 249645 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QP | HR53QP | hr5 3qp | hr53qp | Powys | Powys | Painscastle STW | 6544 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 318764 | 252627 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QQ | HR53QQ | hr5 3qq | hr53qq | Powys | Powys | Painscastle STW | 4797 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 320958 | 249148 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QR | HR53QR | hr5 3qr | hr53qr | Powys | Powys | Hundred House STW | 6637 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 317655 | 254877 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QS | HR53QS | hr5 3qs | hr53qs | Powys | Powys | Painscastle STW | 5983 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 319946 | 251561 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QT | HR53QT | hr5 3qt | hr53qt | Powys | Powys | Painscastle STW | 6941 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 321776 | 251426 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QU | HR53QU | hr5 3qu | hr53qu | Powys | Powys | Painscastle STW | 6763 | 1121 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.89 | 11.14 | 12.32 | 320560 | 252108 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QW | HR53QW | hr5 3qw | hr53qw | Powys | Powys | Painscastle STW | 5803 | 1105 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.6 | 10.98 | 12.14 | 318823 | 251839 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QX | HR53QX | hr5 3qx | hr53qx | Powys | Powys | Painscastle STW | 7424 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 319046 | 253462 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3QZ | HR53QZ | hr5 3qz | hr53qz | Powys | Powys | Painscastle STW | 3627 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 317258 | 249922 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
HR5 3RA | HR53RA | hr5 3ra | hr53ra | Powys | Powys | Old Radnor STW | 6994 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 320820 | 253544 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5AB | LD15AB | ld1 5ab | ld15ab | Powys | Powys | Llanyre WwTW | 1298 | 1078 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.09 | 10.72 | 11.84 | 306543 | 262536 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5AD | LD15AD | ld1 5ad | ld15ad | Powys | Powys | Llanyre WwTW | 1020 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306147 | 261837 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5AE | LD15AE | ld1 5ae | ld15ae | Powys | Powys | Llanyre WwTW | 1914 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 306862 | 261294 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5AF | LD15AF | ld1 5af | ld15af | Powys | Powys | Llanyre WwTW | 1270 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 306518 | 262169 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5AJ | LD15AJ | ld1 5aj | ld15aj | Powys | Powys | Llanyre WwTW | 1182 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306427 | 262155 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5AL | LD15AL | ld1 5al | ld15al | Powys | Powys | Llandrindod Wells STW | 976 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305622 | 259836 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5AN | LD15AN | ld1 5an | ld15an | Powys | Powys | Llanyre WwTW | 1289 | 1112 | 900to1200 | 2.23 | 1.63 | 1.19 | 20.73 | 11.05 | 12.22 | 306467 | 262792 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5AP | LD15AP | ld1 5ap | ld15ap | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BA | LD15BA | ld1 5ba | ld15ba | Powys | Powys | Llanyre WwTW | 1126 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306385 | 262295 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BB | LD15BB | ld1 5bb | ld15bb | Powys | Powys | Llanyre WwTW | 1283 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305968 | 261271 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BD | LD15BD | ld1 5bd | ld15bd | Powys | Powys | Llandrindod Wells STW | 1307 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305991 | 261229 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BE | LD15BE | ld1 5be | ld15be | Powys | Powys | Llanyre WwTW | 1069 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306020 | 261589 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BF | LD15BF | ld1 5bf | ld15bf | Powys | Powys | Llanyre WwTW | 1219 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306478 | 262290 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BG | LD15BG | ld1 5bg | ld15bg | Powys | Powys | Llanyre WwTW | 930 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306153 | 262080 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BH | LD15BH | ld1 5bh | ld15bh | Powys | Powys | Llanyre WwTW | 956 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306190 | 262120 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BJ | LD15BJ | ld1 5bj | ld15bj | Powys | Powys | Llanyre WwTW | 1211 | 1112 | 900to1200 | 2.23 | 1.63 | 1.19 | 20.73 | 11.05 | 12.22 | 306408 | 262723 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BL | LD15BL | ld1 5bl | ld15bl | Powys | Powys | Llanyre WwTW | 1058 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306306 | 262497 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BN | LD15BN | ld1 5bn | ld15bn | Powys | Powys | Llanyre WwTW | 998 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306256 | 262284 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BP | LD15BP | ld1 5bp | ld15bp | Powys | Powys | Llanyre WwTW | 1010 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306267 | 262417 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BQ | LD15BQ | ld1 5bq | ld15bq | Powys | Powys | Llanyre WwTW | 1007 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306156 | 261881 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BS | LD15BS | ld1 5bs | ld15bs | Powys | Powys | Llanyre WwTW | 1005 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306264 | 262376 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BT | LD15BT | ld1 5bt | ld15bt | Powys | Powys | Llanyre WwTW | 997 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306257 | 262349 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BU | LD15BU | ld1 5bu | ld15bu | Powys | Powys | Llanyre WwTW | 983 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306243 | 262325 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BW | LD15BW | ld1 5bw | ld15bw | Powys | Powys | Llanyre WwTW | 1029 | 1112 | 900to1200 | 2.23 | 1.63 | 1.19 | 20.73 | 11.05 | 12.22 | 306276 | 262502 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BX | LD15BX | ld1 5bx | ld15bx | Powys | Powys | Llanyre WwTW | 1097 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306352 | 262444 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BY | LD15BY | ld1 5by | ld15by | Powys | Powys | Llanyre WwTW | 977 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306235 | 262291 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5BZ | LD15BZ | ld1 5bz | ld15bz | Powys | Powys | Llanyre WwTW | 1160 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306417 | 262413 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5DA | LD15DA | ld1 5da | ld15da | Powys | Powys | Llanyre WwTW | 947 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306196 | 262195 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5DB | LD15DB | ld1 5db | ld15db | Powys | Powys | Llanyre WwTW | 937 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306176 | 262143 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5DD | LD15DD | ld1 5dd | ld15dd | Powys | Powys | Penybont STW | 644 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 311182 | 264275 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5DE | LD15DE | ld1 5de | ld15de | Powys | Powys | Llandrindod Wells STW | 1773 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 306590 | 261055 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5DF | LD15DF | ld1 5df | ld15df | Powys | Powys | Llanyre WwTW | 1327 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 306586 | 262393 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5DG | LD15DG | ld1 5dg | ld15dg | Powys | Powys | Llandrindod Wells STW | 1246 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305947 | 261186 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5DH | LD15DH | ld1 5dh | ld15dh | Powys | Powys | Llandrindod Wells STW | 1250 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305971 | 261155 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5DL | LD15DL | ld1 5dl | ld15dl | Powys | Powys | Llandrindod Wells STW | 1331 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306040 | 261198 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5DP | LD15DP | ld1 5dp | ld15dp | Powys | Powys | Llandrindod Wells STW | 1231 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306016 | 261033 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5DU | LD15DU | ld1 5du | ld15du | Powys | Powys | Llandrindod Wells STW | 1257 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306050 | 261021 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5DY | LD15DY | ld1 5dy | ld15dy | Powys | Powys | Llandrindod Wells STW | 1303 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306063 | 261100 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EA | LD15EA | ld1 5ea | ld15ea | Powys | Powys | Llandrindod Wells STW | 1212 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305986 | 261051 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EB | LD15EB | ld1 5eb | ld15eb | Powys | Powys | Llanyre WwTW | 1020 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306108 | 261773 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5ED | LD15ED | ld1 5ed | ld15ed | Powys | Powys | Llandrindod Wells STW | 357 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 305050 | 260173 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EE | LD15EE | ld1 5ee | ld15ee | Powys | Powys | Llandrindod Wells STW | 1400 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306120 | 261199 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EF | LD15EF | ld1 5ef | ld15ef | Powys | Powys | Llanyre WwTW | 1443 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306348 | 261393 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EG | LD15EG | ld1 5eg | ld15eg | Powys | Powys | Llanyre WwTW | 1378 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306331 | 261474 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EH | LD15EH | ld1 5eh | ld15eh | Powys | Powys | Llanyre WwTW | 1501 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306411 | 261378 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EL | LD15EL | ld1 5el | ld15el | Powys | Powys | Llanyre WwTW | 1389 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306153 | 261276 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EP | LD15EP | ld1 5ep | ld15ep | Powys | Powys | Llanyre WwTW | 1102 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306286 | 261938 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EQ | LD15EQ | ld1 5eq | ld15eq | Powys | Powys | Llandrindod Wells STW | 1183 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305958 | 261042 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5ER | LD15ER | ld1 5er | ld15er | Powys | Powys | Llandrindod Wells STW | 1118 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305868 | 261071 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5ES | LD15ES | ld1 5es | ld15es | Powys | Powys | Llandrindod Wells STW | 1275 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306111 | 260918 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5ET | LD15ET | ld1 5et | ld15et | Powys | Powys | Llandrindod Wells STW | 1211 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305912 | 261175 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EU | LD15EU | ld1 5eu | ld15eu | Powys | Powys | Llandrindod Wells STW | 1160 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305886 | 261121 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EW | LD15EW | ld1 5ew | ld15ew | Powys | Powys | Llandrindod Wells STW | 898 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305706 | 260090 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EX | LD15EX | ld1 5ex | ld15ex | Powys | Powys | Llandrindod Wells STW | 825 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305663 | 260170 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5EY | LD15EY | ld1 5ey | ld15ey | Powys | Powys | Llandrindod Wells STW | 1145 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305939 | 260996 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5HA | LD15HA | ld1 5ha | ld15ha | Powys | Powys | Llandrindod Wells STW | 1390 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306214 | 260972 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5HB | LD15HB | ld1 5hb | ld15hb | Powys | Powys | Llandrindod Wells STW | 950 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305690 | 259962 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5HE | LD15HE | ld1 5he | ld15he | Powys | Powys | Llandrindod Wells STW | 1125 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305936 | 260954 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5HF | LD15HF | ld1 5hf | ld15hf | Powys | Powys | Llanyre WwTW | 1280 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306045 | 261330 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5HG | LD15HG | ld1 5hg | ld15hg | Powys | Powys | Llandrindod Wells STW | 1136 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305970 | 260899 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5HP | LD15HP | ld1 5hp | ld15hp | Powys | Powys | Llandrindod Wells STW | 1073 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305961 | 260698 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5HR | LD15HR | ld1 5hr | ld15hr | Powys | Powys | Llandrindod Wells STW | 1114 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305986 | 260774 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5HS | LD15HS | ld1 5hs | ld15hs | Powys | Powys | Llanyre WwTW | 1369 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306092 | 261253 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5HT | LD15HT | ld1 5ht | ld15ht | Powys | Powys | Llandrindod Wells STW | 1567 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306321 | 261175 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5HU | LD15HU | ld1 5hu | ld15hu | Powys | Powys | Llandrindod Wells STW | 1244 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306078 | 260919 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5HW | LD15HW | ld1 5hw | ld15hw | Powys | Powys | Llandrindod Wells STW | 1045 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305924 | 260737 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5HY | LD15HY | ld1 5hy | ld15hy | Powys | Powys | Llanyre WwTW | 1319 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306193 | 261408 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LA | LD15LA | ld1 5la | ld15la | Powys | Powys | Llanyre WwTW | 1283 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306136 | 261403 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LB | LD15LB | ld1 5lb | ld15lb | Powys | Powys | Llanyre WwTW | 1193 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306155 | 261552 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LD | LD15LD | ld1 5ld | ld15ld | Powys | Powys | Llandrindod Wells STW | 1449 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306246 | 261052 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LE | LD15LE | ld1 5le | ld15le | Powys | Powys | Llanyre WwTW | 1932 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 306869 | 261271 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LF | LD15LF | ld1 5lf | ld15lf | Powys | Powys | Llanyre WwTW | 1778 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 306649 | 261231 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LG | LD15LG | ld1 5lg | ld15lg | Powys | Powys | Llandrindod Wells STW | 1460 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306331 | 260821 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LH | LD15LH | ld1 5lh | ld15lh | Powys | Powys | Llanyre WwTW | 1121 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306075 | 261571 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LJ | LD15LJ | ld1 5lj | ld15lj | Powys | Powys | Llanyre WwTW | 1816 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 306672 | 261199 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LL | LD15LL | ld1 5ll | ld15ll | Powys | Powys | Llandrindod Wells STW | 1041 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305901 | 260809 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LN | LD15LN | ld1 5ln | ld15ln | Powys | Powys | Llandrindod Wells STW | 931 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305788 | 260799 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LP | LD15LP | ld1 5lp | ld15lp | Powys | Powys | Llandrindod Wells STW | 991 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305876 | 260708 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LQ | LD15LQ | ld1 5lq | ld15lq | Powys | Powys | Llandrindod Wells STW | 866 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305767 | 260599 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LR | LD15LR | ld1 5lr | ld15lr | Powys | Powys | Llandrindod Wells STW | 977 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305868 | 260674 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LS | LD15LS | ld1 5ls | ld15ls | Powys | Powys | Llandrindod Wells STW | 967 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305863 | 260642 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LT | LD15LT | ld1 5lt | ld15lt | Powys | Powys | Llandrindod Wells STW | 912 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305813 | 260604 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LU | LD15LU | ld1 5lu | ld15lu | Powys | Powys | Llandrindod Wells STW | 974 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305876 | 260597 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LW | LD15LW | ld1 5lw | ld15lw | Powys | Powys | Llandrindod Wells STW | 985 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305848 | 260790 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LX | LD15LX | ld1 5lx | ld15lx | Powys | Powys | Llanyre WwTW | 2134 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 307160 | 261370 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5LY | LD15LY | ld1 5ly | ld15ly | Powys | Powys | Llandrindod Wells STW | 1067 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305967 | 260619 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NA | LD15NA | ld1 5na | ld15na | Powys | Powys | Llandrindod Wells STW | 1012 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305917 | 260449 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NB | LD15NB | ld1 5nb | ld15nb | Powys | Powys | Llandrindod Wells STW | 827 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305705 | 260282 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5ND | LD15ND | ld1 5nd | ld15nd | Powys | Powys | Llandrindod Wells STW | 940 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305512 | 259781 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NE | LD15NE | ld1 5ne | ld15ne | Powys | Powys | Llandrindod Wells STW | 1004 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305908 | 260422 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NF | LD15NF | ld1 5nf | ld15nf | Powys | Powys | Llandrindod Wells STW | 895 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305802 | 260509 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NG | LD15NG | ld1 5ng | ld15ng | Powys | Powys | Llandrindod Wells STW | 871 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305777 | 260471 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NH | LD15NH | ld1 5nh | ld15nh | Powys | Powys | Llandrindod Wells STW | 840 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305743 | 260424 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NL | LD15NL | ld1 5nl | ld15nl | Powys | Powys | Llandrindod Wells STW | 1040 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305614 | 259738 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NN | LD15NN | ld1 5nn | ld15nn | Powys | Powys | Llandrindod Wells STW | 763 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305658 | 260634 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NP | LD15NP | ld1 5np | ld15np | Powys | Powys | Llanyre WwTW | 2070 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 307009 | 261234 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NQ | LD15NQ | ld1 5nq | ld15nq | Powys | Powys | Llandrindod Wells STW | 887 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305748 | 260219 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NR | LD15NR | ld1 5nr | ld15nr | Powys | Powys | Llandrindod Wells STW | 906 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305801 | 260647 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NS | LD15NS | ld1 5ns | ld15ns | Powys | Powys | Llandrindod Wells STW | 877 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305758 | 260290 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NT | LD15NT | ld1 5nt | ld15nt | Powys | Powys | Llandrindod Wells STW | 1196 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 306033 | 260097 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NU | LD15NU | ld1 5nu | ld15nu | Powys | Powys | Llandrindod Wells STW | 1456 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306359 | 260597 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NW | LD15NW | ld1 5nw | ld15nw | Powys | Powys | Llandrindod Wells STW | 962 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305647 | 259886 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NX | LD15NX | ld1 5nx | ld15nx | Powys | Powys | Llandrindod Wells STW | 944 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305836 | 260334 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NY | LD15NY | ld1 5ny | ld15ny | Powys | Powys | Llandrindod Wells STW | 2617 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 307464 | 259947 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5NZ | LD15NZ | ld1 5nz | ld15nz | Powys | Powys | Llandrindod Wells STW | 1085 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305560 | 259634 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PA | LD15PA | ld1 5pa | ld15pa | Powys | Powys | Llandrindod Wells STW | 4371 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 308669 | 258276 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PB | LD15PB | ld1 5pb | ld15pb | Powys | Powys | Llandrindod Wells STW | 2201 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 306131 | 258671 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PD | LD15PD | ld1 5pd | ld15pd | Powys | Powys | Llanyre WwTW | 2671 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 307849 | 261685 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PE | LD15PE | ld1 5pe | ld15pe | Powys | Powys | Llanyre WwTW | 1526 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 306747 | 261999 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PF | LD15PF | ld1 5pf | ld15pf | Powys | Powys | Llanyre WwTW | 1376 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306452 | 261653 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PG | LD15PG | ld1 5pg | ld15pg | Powys | Powys | Llandrindod Wells STW | 2641 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 304951 | 257860 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PH | LD15PH | ld1 5ph | ld15ph | Powys | Powys | Llandrindod Wells STW | 1080 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 305351 | 259516 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PJ | LD15PJ | ld1 5pj | ld15pj | Powys | Powys | Llandrindod Wells STW | 2702 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 304932 | 257799 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PL | LD15PL | ld1 5pl | ld15pl | Powys | Powys | Llandrindod Wells STW | 1329 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305233 | 259212 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PN | LD15PN | ld1 5pn | ld15pn | Powys | Powys | Llandrindod Wells STW | 1415 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305193 | 259115 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PP | LD15PP | ld1 5pp | ld15pp | Powys | Powys | Llandrindod Wells STW | 1430 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 304818 | 259073 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PR | LD15PR | ld1 5pr | ld15pr | Powys | Powys | Llandrindod Wells STW | 1691 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305252 | 258845 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PS | LD15PS | ld1 5ps | ld15ps | Powys | Powys | Llandrindod Wells STW | 1590 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305256 | 258949 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PT | LD15PT | ld1 5pt | ld15pt | Powys | Powys | Llandrindod Wells STW | 1874 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305151 | 258643 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PU | LD15PU | ld1 5pu | ld15pu | Powys | Powys | Llandrindod Wells STW | 2629 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 304813 | 257873 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PW | LD15PW | ld1 5pw | ld15pw | Powys | Powys | Llandrindod Wells STW | 1431 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305120 | 259085 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5PY | LD15PY | ld1 5py | ld15py | Powys | Powys | Llandrindod Wells STW | 2510 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 304930 | 257991 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RA | LD15RA | ld1 5ra | ld15ra | Powys | Powys | Llandrindod Wells STW | 1929 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305214 | 258596 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RB | LD15RB | ld1 5rb | ld15rb | Powys | Powys | Llandrindod Wells STW | 2035 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 305159 | 258481 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RD | LD15RD | ld1 5rd | ld15rd | Powys | Powys | Llandrindod Wells STW | 2231 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 305072 | 258276 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RE | LD15RE | ld1 5re | ld15re | Powys | Powys | Llandrindod Wells STW | 2458 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 305458 | 258105 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RF | LD15RF | ld1 5rf | ld15rf | Powys | Powys | Llandrindod Wells STW | 3623 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 305386 | 256910 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RG | LD15RG | ld1 5rg | ld15rg | Powys | Powys | Newbridge-On-Wye STW | 3156 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 304353 | 256839 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RH | LD15RH | ld1 5rh | ld15rh | Powys | Powys | Llandrindod Wells STW | 3945 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 306987 | 257149 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RJ | LD15RJ | ld1 5rj | ld15rj | Powys | Powys | Llandrindod Wells STW | 2153 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 304980 | 258349 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RL | LD15RL | ld1 5rl | ld15rl | Powys | Powys | Hundred House STW | 3048 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 309017 | 256639 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RN | LD15RN | ld1 5rn | ld15rn | Powys | Powys | Llandrindod Wells STW | 3740 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 306491 | 257113 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RP | LD15RP | ld1 5rp | ld15rp | Powys | Powys | Hundred House STW | 3129 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 311593 | 257439 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RR | LD15RR | ld1 5rr | ld15rr | Powys | Powys | Hundred House STW | 3283 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 313281 | 256758 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RS | LD15RS | ld1 5rs | ld15rs | Powys | Powys | Hundred House STW | 1703 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 309505 | 255096 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RT | LD15RT | ld1 5rt | ld15rt | Powys | Powys | Hundred House STW | 426 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 310625 | 254457 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RU | LD15RU | ld1 5ru | ld15ru | Powys | Powys | Hundred House STW | 2527 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 308610 | 255051 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RW | LD15RW | ld1 5rw | ld15rw | Powys | Powys | Hundred House STW | 2170 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 310599 | 256484 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5RY | LD15RY | ld1 5ry | ld15ry | Powys | Powys | Hundred House STW | 395 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 311377 | 254566 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SA | LD15SA | ld1 5sa | ld15sa | Powys | Powys | Hundred House STW | 1948 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 311837 | 256137 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SB | LD15SB | ld1 5sb | ld15sb | Powys | Powys | Hundred House STW | 1357 | 1038 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.35 | 10.32 | 11.4 | 312015 | 253417 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SD | LD15SD | ld1 5sd | ld15sd | Powys | Powys | Hundred House STW | 2321 | 1039 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.37 | 10.33 | 11.42 | 312995 | 253110 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SE | LD15SE | ld1 5se | ld15se | Powys | Powys | Hundred House STW | 4628 | 1042 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.42 | 10.36 | 11.45 | 315478 | 253053 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SF | LD15SF | ld1 5sf | ld15sf | Powys | Powys | Hundred House STW | 2487 | 1060 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.76 | 10.54 | 11.65 | 312436 | 252303 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SH | LD15SH | ld1 5sh | ld15sh | Powys | Powys | Llandrindod Wells STW | 2075 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 306906 | 261053 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SJ | LD15SJ | ld1 5sj | ld15sj | Powys | Powys | Llandrindod Wells STW | 2133 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 305035 | 258371 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SL | LD15SL | ld1 5sl | ld15sl | Powys | Powys | Crossgates STW | 1907 | 1078 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.09 | 10.72 | 11.84 | 306986 | 263328 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SN | LD15SN | ld1 5sn | ld15sn | Powys | Powys | Crossgates STW | 410 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 308758 | 264638 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SP | LD15SP | ld1 5sp | ld15sp | Powys | Powys | Penybont STW | 3120 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 311406 | 260774 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SQ | LD15SQ | ld1 5sq | ld15sq | Powys | Powys | Crossgates STW | 822 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 309361 | 264668 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SR | LD15SR | ld1 5sr | ld15sr | Powys | Powys | Penybont STW | 3244 | 1115 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.78 | 11.08 | 12.25 | 310395 | 260907 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SS | LD15SS | ld1 5ss | ld15ss | Powys | Powys | Crossgates STW | 1141 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 308463 | 263116 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5ST | LD15ST | ld1 5st | ld15st | Powys | Powys | Crossgates STW | 235 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 308490 | 264402 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SU | LD15SU | ld1 5su | ld15su | Powys | Powys | Crossgates STW | 847 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 309496 | 264374 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SW | LD15SW | ld1 5sw | ld15sw | Powys | Powys | Penybont STW | 1442 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 310708 | 262825 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5SY | LD15SY | ld1 5sy | ld15sy | Powys | Powys | Penybont STW | 1043 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 310687 | 264165 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TA | LD15TA | ld1 5ta | ld15ta | Powys | Powys | Penybont STW | 565 | 1042 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.42 | 10.36 | 11.45 | 311713 | 264444 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TB | LD15TB | ld1 5tb | ld15tb | Powys | Powys | Penybont STW | 2377 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 313383 | 265547 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TD | LD15TD | ld1 5td | ld15td | Powys | Powys | Llandegley STW | 3147 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 314889 | 266054 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TE | LD15TE | ld1 5te | ld15te | Powys | Powys | Llandegley STW | 3829 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 314285 | 266904 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TF | LD15TF | ld1 5tf | ld15tf | Powys | Powys | Llandegley STW | 4051 | 1126 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.99 | 11.19 | 12.37 | 314594 | 267077 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TG | LD15TG | ld1 5tg | ld15tg | Powys | Powys | Llandewi Ystradenny STW | 3583 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 313958 | 267068 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TH | LD15TH | ld1 5th | ld15th | Powys | Powys | Llandegley STW | 3676 | 1118 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.84 | 11.11 | 12.28 | 315291 | 266460 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TL | LD15TL | ld1 5tl | ld15tl | Powys | Powys | Llandegley STW | 4638 | 1143 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.3 | 11.36 | 12.56 | 315988 | 267187 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TN | LD15TN | ld1 5tn | ld15tn | Powys | Powys | Llangunllo STW | 4329 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 317945 | 268291 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TP | LD15TP | ld1 5tp | ld15tp | Powys | Powys | Llandrindod Wells STW | 2597 | 1093 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.37 | 10.86 | 12.01 | 304890 | 257904 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TS | LD15TS | ld1 5ts | ld15ts | Powys | Powys | Llandrindod Wells STW | 924 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 305797 | 260251 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TT | LD15TT | ld1 5tt | ld15tt | Powys | Powys | Crossgates STW | 910 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 309093 | 263440 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TU | LD15TU | ld1 5tu | ld15tu | Powys | Powys | Penybont STW | 1329 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 310645 | 264700 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TW | LD15TW | ld1 5tw | ld15tw | Powys | Powys | Llandegley STW | 4646 | 1143 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.3 | 11.36 | 12.56 | 315672 | 267352 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5TY | LD15TY | ld1 5ty | ld15ty | Powys | Powys | Penybont STW | 349 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 311353 | 263971 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UA | LD15UA | ld1 5ua | ld15ua | Powys | Powys | Penybont STW | 252 | 1042 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.42 | 10.36 | 11.45 | 311570 | 264102 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UB | LD15UB | ld1 5ub | ld15ub | Powys | Powys | Penybont STW | 178 | 1042 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.42 | 10.36 | 11.45 | 311799 | 263739 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UD | LD15UD | ld1 5ud | ld15ud | Powys | Powys | Llandegley STW | 462 | 1078 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.09 | 10.72 | 11.84 | 313328 | 263017 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UE | LD15UE | ld1 5ue | ld15ue | Powys | Powys | Llandegley STW | 1554 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 312576 | 262129 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UF | LD15UF | ld1 5uf | ld15uf | Powys | Powys | Llandegley STW | 390 | 1139 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.23 | 11.32 | 12.51 | 314066 | 262845 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UG | LD15UG | ld1 5ug | ld15ug | Powys | Powys | Llandegley STW | 2588 | 1076 | 900to1200 | 2.15 | 1.58 | 1.16 | 20.05 | 10.7 | 11.82 | 314695 | 260690 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UH | LD15UH | ld1 5uh | ld15uh | Powys | Powys | Llandegley STW | 1074 | 1154 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.51 | 11.47 | 12.68 | 314326 | 264035 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UL | LD15UL | ld1 5ul | ld15ul | Powys | Powys | Llandrindod Wells STW | 1221 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305902 | 261207 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UN | LD15UN | ld1 5un | ld15un | Powys | Powys | Llandewi Ystradenny STW | 5626 | 1134 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.14 | 11.27 | 12.46 | 316126 | 268905 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UP | LD15UP | ld1 5up | ld15up | Powys | Powys | Llangunllo STW | 3340 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 318348 | 272066 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UR | LD15UR | ld1 5ur | ld15ur | Powys | Powys | Llangunllo STW | 2418 | 1143 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.3 | 11.36 | 12.56 | 319034 | 270748 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5US | LD15US | ld1 5us | ld15us | Powys | Powys | Penybont STW | 98 | 1042 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.42 | 10.36 | 11.45 | 311674 | 263977 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UT | LD15UT | ld1 5ut | ld15ut | Powys | Powys | Llangunllo STW | 3314 | 1180 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.99 | 11.73 | 12.96 | 318544 | 272421 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5UW | LD15UW | ld1 5uw | ld15uw | Powys | Powys | Llangunllo STW | 4331 | 1154 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.51 | 11.47 | 12.68 | 317128 | 271083 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5WA | LD15WA | ld1 5wa | ld15wa | Powys | Powys | Llandrindod Wells STW | 1566 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306381 | 261027 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5WF | LD15WF | ld1 5wf | ld15wf | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5YA | LD15YA | ld1 5ya | ld15ya | Powys | Powys | Llanyre WwTW | 1082 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306154 | 261731 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5YB | LD15YB | ld1 5yb | ld15yb | Powys | Powys | Llanyre WwTW | 1122 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306193 | 261717 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5YD | LD15YD | ld1 5yd | ld15yd | Powys | Powys | Llanyre WwTW | 1184 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306242 | 261679 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5YE | LD15YE | ld1 5ye | ld15ye | Powys | Powys | Llanyre WwTW | 1172 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306284 | 261770 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5YF | LD15YF | ld1 5yf | ld15yf | Powys | Powys | Llanyre WwTW | 1141 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306295 | 261860 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 5ZG | LD15ZG | ld1 5zg | ld15zg | Powys | Powys | Llandrindod Wells STW | 1473 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306339 | 260844 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AA | LD16AA | ld1 6aa | ld16aa | Powys | Powys | Llandrindod Wells STW | 967 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305683 | 261076 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AB | LD16AB | ld1 6ab | ld16ab | Powys | Powys | Llandrindod Wells STW | 1032 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305759 | 261082 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AE | LD16AE | ld1 6ae | ld16ae | Powys | Powys | Llandrindod Wells STW | 728 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305519 | 260894 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AF | LD16AF | ld1 6af | ld16af | Powys | Powys | Llandrindod Wells STW | 895 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305563 | 261109 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AG | LD16AG | ld1 6ag | ld16ag | Powys | Powys | Llandrindod Wells STW | 1103 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305771 | 261185 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AH | LD16AH | ld1 6ah | ld16ah | Powys | Powys | Llandrindod Wells STW | 1118 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305685 | 261303 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AJ | LD16AJ | ld1 6aj | ld16aj | Powys | Powys | Llandrindod Wells STW | 906 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305507 | 261178 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AL | LD16AL | ld1 6al | ld16al | Powys | Powys | Llandrindod Wells STW | 1087 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305715 | 261226 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AN | LD16AN | ld1 6an | ld16an | Powys | Powys | Llanyre WwTW | 1071 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305669 | 261351 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AP | LD16AP | ld1 6ap | ld16ap | Powys | Powys | Llandrindod Wells STW | 1051 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305553 | 261329 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AQ | LD16AQ | ld1 6aq | ld16aq | Powys | Powys | Llanyre WwTW | 1028 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305652 | 261390 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AR | LD16AR | ld1 6ar | ld16ar | Powys | Powys | Llandrindod Wells STW | 866 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305461 | 261165 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AS | LD16AS | ld1 6as | ld16as | Powys | Powys | Llanyre WwTW | 988 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305439 | 261369 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AT | LD16AT | ld1 6at | ld16at | Powys | Powys | Llandrindod Wells STW | 893 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305610 | 261051 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AU | LD16AU | ld1 6au | ld16au | Powys | Powys | Llandrindod Wells STW | 940 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305735 | 260944 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AW | LD16AW | ld1 6aw | ld16aw | Powys | Powys | Llanyre WwTW | 885 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305551 | 261504 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AX | LD16AX | ld1 6ax | ld16ax | Powys | Powys | Llandrindod Wells STW | 814 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 305493 | 261064 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AY | LD16AY | ld1 6ay | ld16ay | Powys | Powys | Llandrindod Wells STW | 959 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305726 | 260999 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6AZ | LD16AZ | ld1 6az | ld16az | Powys | Powys | Llanyre WwTW | 1201 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305829 | 261283 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BA | LD16BA | ld1 6ba | ld16ba | Powys | Powys | Llandrindod Wells STW | 1007 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305646 | 261183 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BB | LD16BB | ld1 6bb | ld16bb | Powys | Powys | Llanyre WwTW | 668 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305859 | 262044 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BD | LD16BD | ld1 6bd | ld16bd | Powys | Powys | Llanyre WwTW | 673 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305772 | 261904 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BE | LD16BE | ld1 6be | ld16be | Powys | Powys | Llanyre WwTW | 704 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305812 | 261904 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BG | LD16BG | ld1 6bg | ld16bg | Powys | Powys | Llanyre WwTW | 1124 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305826 | 261369 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BH | LD16BH | ld1 6bh | ld16bh | Powys | Powys | Llanyre WwTW | 953 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305898 | 261632 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BJ | LD16BJ | ld1 6bj | ld16bj | Powys | Powys | Llanyre WwTW | 815 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305731 | 261675 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BL | LD16BL | ld1 6bl | ld16bl | Powys | Powys | Llanyre WwTW | 903 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306061 | 261923 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BN | LD16BN | ld1 6bn | ld16bn | Powys | Powys | Llanyre WwTW | 645 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305776 | 261954 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BP | LD16BP | ld1 6bp | ld16bp | Powys | Powys | Llanyre WwTW | 733 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305950 | 262094 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BS | LD16BS | ld1 6bs | ld16bs | Powys | Powys | Llanyre WwTW | 905 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306011 | 261835 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BT | LD16BT | ld1 6bt | ld16bt | Powys | Powys | Llanyre WwTW | 876 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306000 | 261872 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BU | LD16BU | ld1 6bu | ld16bu | Powys | Powys | Llanyre WwTW | 875 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306025 | 261915 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BW | LD16BW | ld1 6bw | ld16bw | Powys | Powys | Llanyre WwTW | 601 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305789 | 262056 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BX | LD16BX | ld1 6bx | ld16bx | Powys | Powys | Llanyre WwTW | 860 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306048 | 261996 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BY | LD16BY | ld1 6by | ld16by | Powys | Powys | Llanyre WwTW | 552 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305797 | 262213 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6BZ | LD16BZ | ld1 6bz | ld16bz | Powys | Powys | Llanyre WwTW | 1059 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305806 | 261433 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DA | LD16DA | ld1 6da | ld16da | Powys | Powys | Llanyre WwTW | 415 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305595 | 262095 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DB | LD16DB | ld1 6db | ld16db | Powys | Powys | Llanyre WwTW | 832 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306054 | 262091 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DD | LD16DD | ld1 6dd | ld16dd | Powys | Powys | Llanyre WwTW | 843 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306055 | 262059 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DE | LD16DE | ld1 6de | ld16de | Powys | Powys | Llanyre WwTW | 803 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306019 | 262079 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DF | LD16DF | ld1 6df | ld16df | Powys | Powys | Llanyre WwTW | 909 | 1112 | 900to1200 | 2.23 | 1.63 | 1.19 | 20.73 | 11.05 | 12.22 | 306132 | 262596 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DG | LD16DG | ld1 6dg | ld16dg | Powys | Powys | Llanyre WwTW | 574 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305773 | 262082 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DH | LD16DH | ld1 6dh | ld16dh | Powys | Powys | Llanyre WwTW | 606 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305819 | 262106 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DJ | LD16DJ | ld1 6dj | ld16dj | Powys | Powys | Llanyre WwTW | 730 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305935 | 262062 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DL | LD16DL | ld1 6dl | ld16dl | Powys | Powys | Llanyre WwTW | 523 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305712 | 262077 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DN | LD16DN | ld1 6dn | ld16dn | Powys | Powys | Llanyre WwTW | 490 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305596 | 261983 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DP | LD16DP | ld1 6dp | ld16dp | Powys | Powys | Llanyre WwTW | 726 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305747 | 261802 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DQ | LD16DQ | ld1 6dq | ld16dq | Powys | Powys | Llanyre WwTW | 781 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305950 | 261974 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DR | LD16DR | ld1 6dr | ld16dr | Powys | Powys | Llanyre WwTW | 611 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305706 | 261923 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DS | LD16DS | ld1 6ds | ld16ds | Powys | Powys | Llanyre WwTW | 557 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305720 | 262026 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DT | LD16DT | ld1 6dt | ld16dt | Powys | Powys | Llanyre WwTW | 905 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 304462 | 262767 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DU | LD16DU | ld1 6du | ld16du | Powys | Powys | Llanyre WwTW | 511 | 1115 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.78 | 11.08 | 12.25 | 305420 | 261855 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DW | LD16DW | ld1 6dw | ld16dw | Powys | Powys | Llanyre WwTW | 526 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305625 | 261962 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DX | LD16DX | ld1 6dx | ld16dx | Powys | Powys | Llanyre WwTW | 984 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 304320 | 262631 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DY | LD16DY | ld1 6dy | ld16dy | Powys | Powys | Llanyre WwTW | 1024 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 304252 | 262518 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6DZ | LD16DZ | ld1 6dz | ld16dz | Powys | Powys | Llanyre WwTW | 848 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305947 | 261843 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EA | LD16EA | ld1 6ea | ld16ea | Powys | Powys | Llanyre WwTW | 1123 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 304401 | 263063 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EB | LD16EB | ld1 6eb | ld16eb | Powys | Powys | Llanyre WwTW | 1411 | 1155 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.53 | 11.48 | 12.69 | 304621 | 263597 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6ED | LD16ED | ld1 6ed | ld16ed | Powys | Powys | Llanyre WwTW | 2072 | 1155 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.53 | 11.48 | 12.69 | 305456 | 264402 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EE | LD16EE | ld1 6ee | ld16ee | Powys | Powys | Llanyre WwTW | 2527 | 1195 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.27 | 11.88 | 13.13 | 303357 | 264002 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EF | LD16EF | ld1 6ef | ld16ef | Powys | Powys | Llanyre WwTW | 2932 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 303935 | 264955 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EG | LD16EG | ld1 6eg | ld16eg | Powys | Powys | Llanyre WwTW | 3384 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 305524 | 265713 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EH | LD16EH | ld1 6eh | ld16eh | Powys | Powys | Abbeycwmhir WwTW | 4031 | 1155 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.53 | 11.48 | 12.69 | 304330 | 267146 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EJ | LD16EJ | ld1 6ej | ld16ej | Powys | Powys | Llanyre WwTW | 402 | 1115 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.78 | 11.08 | 12.25 | 305482 | 262005 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EL | LD16EL | ld1 6el | ld16el | Powys | Powys | Llanyre WwTW | 3746 | 1133 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.12 | 11.26 | 12.45 | 303959 | 265852 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EN | LD16EN | ld1 6en | ld16en | Powys | Powys | Llanyre WwTW | 4567 | 1180 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.99 | 11.73 | 12.96 | 303010 | 266313 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EP | LD16EP | ld1 6ep | ld16ep | Powys | Powys | Llanyre WwTW | 442 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305702 | 262348 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6ER | LD16ER | ld1 6er | ld16er | Powys | Powys | Llanyre WwTW | 808 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306001 | 262018 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6ES | LD16ES | ld1 6es | ld16es | Powys | Powys | Llanyre WwTW | 768 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305908 | 261929 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6ET | LD16ET | ld1 6et | ld16et | Powys | Powys | Llanyre WwTW | 944 | 1115 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.78 | 11.08 | 12.25 | 304819 | 261506 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EU | LD16EU | ld1 6eu | ld16eu | Powys | Powys | Llanyre WwTW | 1086 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 304260 | 261917 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EW | LD16EW | ld1 6ew | ld16ew | Powys | Powys | Rhayader STW | 4202 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 301708 | 265675 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6EY | LD16EY | ld1 6ey | ld16ey | Powys | Powys | Llandrindod Wells STW | 2251 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 302671 | 260758 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HA | LD16HA | ld1 6ha | ld16ha | Powys | Powys | Newbridge-On-Wye STW | 854 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 301739 | 258930 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HB | LD16HB | ld1 6hb | ld16hb | Powys | Powys | Newbridge-On-Wye STW | 2027 | 1254 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.37 | 12.47 | 13.78 | 301575 | 260144 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HD | LD16HD | ld1 6hd | ld16hd | Powys | Powys | Llanwrthwl STW | 3363 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 301091 | 262892 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HE | LD16HE | ld1 6he | ld16he | Powys | Powys | Llanwrthwl STW | 3090 | 1273 | 1200to1500 | 2.55 | 1.86 | 1.37 | 23.73 | 12.65 | 13.99 | 300288 | 261575 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HF | LD16HF | ld1 6hf | ld16hf | Powys | Powys | Llanwrthwl STW | 2228 | 1279 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.84 | 12.71 | 14.05 | 299918 | 262800 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HG | LD16HG | ld1 6hg | ld16hg | Powys | Powys | Llanwrthwl STW | 2130 | 1279 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.84 | 12.71 | 14.05 | 299731 | 262544 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HH | LD16HH | ld1 6hh | ld16hh | Powys | Powys | Llanwrthwl STW | 1797 | 1331 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.81 | 13.23 | 14.62 | 299482 | 262839 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HL | LD16HL | ld1 6hl | ld16hl | Powys | Powys | Llandrindod Wells STW | 2999 | 1305 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.32 | 12.97 | 14.34 | 302239 | 261867 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HN | LD16HN | ld1 6hn | ld16hn | Powys | Powys | Crossgates STW | 716 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 309064 | 264831 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HP | LD16HP | ld1 6hp | ld16hp | Powys | Powys | Llandrindod Wells STW | 1694 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 303215 | 260581 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HR | LD16HR | ld1 6hr | ld16hr | Powys | Powys | Newbridge-On-Wye STW | 1249 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 302505 | 258819 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HS | LD16HS | ld1 6hs | ld16hs | Powys | Powys | Newbridge-On-Wye STW | 977 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 302302 | 258632 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HT | LD16HT | ld1 6ht | ld16ht | Powys | Powys | Newbridge-On-Wye STW | 397 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301820 | 258307 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HU | LD16HU | ld1 6hu | ld16hu | Powys | Powys | Newbridge-On-Wye STW | 298 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301752 | 258217 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HW | LD16HW | ld1 6hw | ld16hw | Powys | Powys | Newbridge-On-Wye STW | 373 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301822 | 258243 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6HY | LD16HY | ld1 6hy | ld16hy | Powys | Powys | Newbridge-On-Wye STW | 283 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301708 | 258273 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LA | LD16LA | ld1 6la | ld16la | Powys | Powys | Newbridge-On-Wye STW | 194 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301647 | 258199 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LB | LD16LB | ld1 6lb | ld16lb | Powys | Powys | Newbridge-On-Wye STW | 187 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301653 | 258159 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LD | LD16LD | ld1 6ld | ld16ld | Powys | Powys | Newbridge-On-Wye STW | 223 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301693 | 258126 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LE | LD16LE | ld1 6le | ld16le | Powys | Powys | Newbridge-On-Wye STW | 385 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301741 | 258394 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LF | LD16LF | ld1 6lf | ld16lf | Powys | Powys | Newbridge-On-Wye STW | 309 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301761 | 258017 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LG | LD16LG | ld1 6lg | ld16lg | Powys | Powys | Newbridge-On-Wye STW | 299 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301683 | 257910 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LH | LD16LH | ld1 6lh | ld16lh | Powys | Powys | Newbridge-On-Wye STW | 216 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301563 | 258315 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LL | LD16LL | ld1 6ll | ld16ll | Powys | Powys | Newbridge-On-Wye STW | 256 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301510 | 258373 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LN | LD16LN | ld1 6ln | ld16ln | Powys | Powys | Newbridge-On-Wye STW | 356 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301534 | 258470 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LP | LD16LP | ld1 6lp | ld16lp | Powys | Powys | Newbridge-On-Wye STW | 453 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 301633 | 258542 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LQ | LD16LQ | ld1 6lq | ld16lq | Powys | Powys | Newbridge-On-Wye STW | 376 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301626 | 258462 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LR | LD16LR | ld1 6lr | ld16lr | Powys | Powys | Newbridge-On-Wye STW | 478 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 301582 | 258585 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LS | LD16LS | ld1 6ls | ld16ls | Powys | Powys | Newbridge-On-Wye STW | 460 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 301655 | 258541 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LT | LD16LT | ld1 6lt | ld16lt | Powys | Powys | Newbridge-On-Wye STW | 348 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301512 | 258465 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LU | LD16LU | ld1 6lu | ld16lu | Powys | Powys | Newbridge-On-Wye STW | 497 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301663 | 257662 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LW | LD16LW | ld1 6lw | ld16lw | Powys | Powys | Newbridge-On-Wye STW | 413 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 301532 | 258528 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LX | LD16LX | ld1 6lx | ld16lx | Powys | Powys | Newbridge-On-Wye STW | 293 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301595 | 257855 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LY | LD16LY | ld1 6ly | ld16ly | Powys | Powys | Newbridge-On-Wye STW | 288 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 301423 | 258404 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6LZ | LD16LZ | ld1 6lz | ld16lz | Powys | Powys | Newbridge-On-Wye STW | 212 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301614 | 257965 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NA | LD16NA | ld1 6na | ld16na | Powys | Powys | Newbridge-On-Wye STW | 467 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301916 | 257981 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NB | LD16NB | ld1 6nb | ld16nb | Powys | Powys | Newbridge-On-Wye STW | 887 | 1284 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.93 | 12.76 | 14.11 | 300681 | 258525 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6ND | LD16ND | ld1 6nd | ld16nd | Powys | Powys | Newbridge-On-Wye STW | 2518 | 1448 | 1200to1500 | 2.9 | 2.12 | 1.56 | 26.99 | 14.39 | 15.91 | 299444 | 259614 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NE | LD16NE | ld1 6ne | ld16ne | Powys | Powys | Newbridge-On-Wye STW | 364 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301832 | 258160 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NF | LD16NF | ld1 6nf | ld16nf | Powys | Powys | Llanyre WwTW | 1096 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 304365 | 262972 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NG | LD16NG | ld1 6ng | ld16ng | Powys | Powys | Llanyre WwTW | 867 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 304446 | 262639 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NL | LD16NL | ld1 6nl | ld16nl | Powys | Powys | Llandrindod Wells STW | 2402 | 1112 | 900to1200 | 2.23 | 1.63 | 1.19 | 20.73 | 11.05 | 12.22 | 304347 | 258165 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NN | LD16NN | ld1 6nn | ld16nn | Powys | Powys | Llanwrthwl STW | 286 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 297919 | 263588 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NP | LD16NP | ld1 6np | ld16np | Powys | Powys | Llanwrthwl STW | 1290 | 1430 | 1200to1500 | 2.86 | 2.09 | 1.54 | 26.65 | 14.21 | 15.71 | 297177 | 264500 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NR | LD16NR | ld1 6nr | ld16nr | Powys | Powys | Llanwrthwl STW | 556 | 1430 | 1200to1500 | 2.86 | 2.09 | 1.54 | 26.65 | 14.21 | 15.71 | 297488 | 263835 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NS | LD16NS | ld1 6ns | ld16ns | Powys | Powys | Llanwrthwl STW | 475 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 297555 | 263778 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NT | LD16NT | ld1 6nt | ld16nt | Powys | Powys | Llanwrthwl STW | 43 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 297718 | 263359 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NU | LD16NU | ld1 6nu | ld16nu | Powys | Powys | Llanwrthwl STW | 1193 | 1430 | 1200to1500 | 2.86 | 2.09 | 1.54 | 26.65 | 14.21 | 15.71 | 296692 | 263881 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NW | LD16NW | ld1 6nw | ld16nw | Powys | Powys | Llanwrthwl STW | 1946 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 297244 | 265226 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6NY | LD16NY | ld1 6ny | ld16ny | Powys | Powys | Elan Village STW | 1238 | 1345 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.07 | 13.37 | 14.78 | 294796 | 265530 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PA | LD16PA | ld1 6pa | ld16pa | Powys | Powys | Llanwrthwl STW | 2152 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 299348 | 264801 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PB | LD16PB | ld1 6pb | ld16pb | Powys | Powys | Llanwrthwl STW | 3888 | 1211 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.57 | 12.04 | 13.31 | 301490 | 264443 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PD | LD16PD | ld1 6pd | ld16pd | Powys | Powys | Llanwrthwl STW | 2142 | 1269 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.65 | 12.61 | 13.94 | 299744 | 264157 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PE | LD16PE | ld1 6pe | ld16pe | Powys | Powys | Llanyre WwTW | 759 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305992 | 262141 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PF | LD16PF | ld1 6pf | ld16pf | Powys | Powys | Llanyre WwTW | 825 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306060 | 262141 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PG | LD16PG | ld1 6pg | ld16pg | Powys | Powys | Llandewi Ystradenny STW | 2796 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 307824 | 268788 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PH | LD16PH | ld1 6ph | ld16ph | Powys | Powys | Abbeycwmhir WwTW | 146 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 305501 | 271136 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PL | LD16PL | ld1 6pl | ld16pl | Powys | Powys | Abbeycwmhir WwTW | 564 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 304968 | 270968 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PN | LD16PN | ld1 6pn | ld16pn | Powys | Powys | Abbeycwmhir WwTW | 1683 | 1277 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.8 | 12.69 | 14.03 | 303918 | 270514 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PP | LD16PP | ld1 6pp | ld16pp | Powys | Powys | Abbeycwmhir WwTW | 3762 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 303955 | 274408 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PR | LD16PR | ld1 6pr | ld16pr | Powys | Powys | Abbeycwmhir WwTW | 4089 | 1191 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.2 | 11.84 | 13.09 | 304567 | 274966 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PS | LD16PS | ld1 6ps | ld16ps | Powys | Powys | Abbeycwmhir WwTW | 4663 | 1161 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.64 | 11.54 | 12.76 | 305114 | 275636 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PT | LD16PT | ld1 6pt | ld16pt | Powys | Powys | Abbeycwmhir WwTW | 3048 | 1238 | 1200to1500 | 2.48 | 1.81 | 1.33 | 23.07 | 12.31 | 13.6 | 306327 | 273934 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PU | LD16PU | ld1 6pu | ld16pu | Powys | Powys | Abbeycwmhir WwTW | 2892 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 307858 | 272708 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6PW | LD16PW | ld1 6pw | ld16pw | Powys | Powys | Abbeycwmhir WwTW | 1727 | 1272 | 1200to1500 | 2.55 | 1.86 | 1.37 | 23.71 | 12.64 | 13.98 | 304223 | 272120 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RA | LD16RA | ld1 6ra | ld16ra | Powys | Powys | Crossgates STW | 453 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 308747 | 264684 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RB | LD16RB | ld1 6rb | ld16rb | Powys | Powys | Crossgates STW | 603 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 308808 | 264824 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RD | LD16RD | ld1 6rd | ld16rd | Powys | Powys | Crossgates STW | 604 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 308829 | 264820 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RE | LD16RE | ld1 6re | ld16re | Powys | Powys | Crossgates STW | 840 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 309289 | 264796 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RF | LD16RF | ld1 6rf | ld16rf | Powys | Powys | Crossgates STW | 975 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 308200 | 265099 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RG | LD16RG | ld1 6rg | ld16rg | Powys | Powys | Crossgates STW | 1498 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 307465 | 265142 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RH | LD16RH | ld1 6rh | ld16rh | Powys | Powys | Crossgates STW | 1871 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 306891 | 264849 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RJ | LD16RJ | ld1 6rj | ld16rj | Powys | Powys | Crossgates STW | 617 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 308694 | 264856 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RL | LD16RL | ld1 6rl | ld16rl | Powys | Powys | Crossgates STW | 1577 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 307599 | 265406 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RN | LD16RN | ld1 6rn | ld16rn | Powys | Powys | Crossgates STW | 2239 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 306902 | 265625 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RP | LD16RP | ld1 6rp | ld16rp | Powys | Powys | Crossgates STW | 1094 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 309001 | 265279 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RQ | LD16RQ | ld1 6rq | ld16rq | Powys | Powys | Crossgates STW | 2389 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 306707 | 265615 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RR | LD16RR | ld1 6rr | ld16rr | Powys | Powys | Crossgates STW | 1547 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 309054 | 265736 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RS | LD16RS | ld1 6rs | ld16rs | Powys | Powys | Crossgates STW | 1639 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 308809 | 265872 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RT | LD16RT | ld1 6rt | ld16rt | Powys | Powys | Llandewi Ystradenny STW | 1561 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 309651 | 266894 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RU | LD16RU | ld1 6ru | ld16ru | Powys | Powys | Crossgates STW | 1819 | 1038 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.35 | 10.32 | 11.4 | 309540 | 265831 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RW | LD16RW | ld1 6rw | ld16rw | Powys | Powys | Crossgates STW | 1983 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 307497 | 265846 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RX | LD16RX | ld1 6rx | ld16rx | Powys | Powys | Crossgates STW | 660 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 308541 | 264889 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6RY | LD16RY | ld1 6ry | ld16ry | Powys | Powys | Crossgates STW | 808 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 308763 | 265041 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SA | LD16SA | ld1 6sa | ld16sa | Powys | Powys | Crossgates STW | 736 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 308556 | 264968 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SB | LD16SB | ld1 6sb | ld16sb | Powys | Powys | Crossgates STW | 1610 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 309164 | 265769 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SD | LD16SD | ld1 6sd | ld16sd | Powys | Powys | Llandewi Ystradenny STW | 1156 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 309488 | 267714 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SE | LD16SE | ld1 6se | ld16se | Powys | Powys | Llandewi Ystradenny STW | 416 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 310680 | 268565 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SF | LD16SF | ld1 6sf | ld16sf | Powys | Powys | Llandewi Ystradenny STW | 684 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 310792 | 268810 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SG | LD16SG | ld1 6sg | ld16sg | Powys | Powys | Llandewi Ystradenny STW | 899 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 310875 | 269008 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SH | LD16SH | ld1 6sh | ld16sh | Powys | Powys | Llandewi Ystradenny STW | 2250 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 310462 | 270418 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SJ | LD16SJ | ld1 6sj | ld16sj | Powys | Powys | Llandewi Ystradenny STW | 633 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 310788 | 268756 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SL | LD16SL | ld1 6sl | ld16sl | Powys | Powys | Llandewi Ystradenny STW | 1378 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 311910 | 267953 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SN | LD16SN | ld1 6sn | ld16sn | Powys | Powys | Llandewi Ystradenny STW | 3262 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 313543 | 269464 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SP | LD16SP | ld1 6sp | ld16sp | Powys | Powys | Llandewi Ystradenny STW | 5120 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 315169 | 270375 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SR | LD16SR | ld1 6sr | ld16sr | Powys | Powys | Llanbister STW | 5018 | 1140 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.25 | 11.33 | 12.53 | 315269 | 271272 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SS | LD16SS | ld1 6ss | ld16ss | Powys | Powys | Llanbister STW | 3129 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 313788 | 272613 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6ST | LD16ST | ld1 6st | ld16st | Powys | Powys | Llanbister STW | 2978 | 1105 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.6 | 10.98 | 12.14 | 313210 | 271808 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SW | LD16SW | ld1 6sw | ld16sw | Powys | Powys | Llandewi Ystradenny STW | 3123 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 313580 | 268921 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6SY | LD16SY | ld1 6sy | ld16sy | Powys | Powys | Llanbister STW | 4292 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 314269 | 271032 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TA | LD16TA | ld1 6ta | ld16ta | Powys | Powys | Crossgates STW | 805 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 308674 | 265045 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TB | LD16TB | ld1 6tb | ld16tb | Powys | Powys | Crossgates STW | 722 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 308629 | 264961 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TD | LD16TD | ld1 6td | ld16td | Powys | Powys | Llanbister STW | 140 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 310805 | 273430 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TE | LD16TE | ld1 6te | ld16te | Powys | Powys | Llandewi Ystradenny STW | 574 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 310802 | 268686 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TF | LD16TF | ld1 6tf | ld16tf | Powys | Powys | Llandewi Ystradenny STW | 1027 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 310865 | 269147 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TG | LD16TG | ld1 6tg | ld16tg | Powys | Powys | Llanbister STW | 1682 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 310909 | 275249 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TH | LD16TH | ld1 6th | ld16th | Powys | Powys | Llanbister STW | 1698 | 1140 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.25 | 11.33 | 12.53 | 310080 | 272038 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TJ | LD16TJ | ld1 6tj | ld16tj | Powys | Powys | Crossgates STW | 820 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 308588 | 265057 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TL | LD16TL | ld1 6tl | ld16tl | Powys | Powys | Llanbister STW | 1856 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 312662 | 273460 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TN | LD16TN | ld1 6tn | ld16tn | Powys | Powys | Llanbister STW | 333 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 310930 | 273259 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TP | LD16TP | ld1 6tp | ld16tp | Powys | Powys | Llanbister STW | 58 | 1140 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.25 | 11.33 | 12.53 | 310764 | 273606 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TR | LD16TR | ld1 6tr | ld16tr | Powys | Powys | Llanbister STW | 796 | 1135 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.15 | 11.28 | 12.47 | 310212 | 274095 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TS | LD16TS | ld1 6ts | ld16ts | Powys | Powys | Llanbister STW | 1416 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 309495 | 274095 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TT | LD16TT | ld1 6tt | ld16tt | Powys | Powys | Llanbister STW | 2611 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 308497 | 274780 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TU | LD16TU | ld1 6tu | ld16tu | Powys | Powys | Llanbadarn Ffynydd STW | 1591 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 309034 | 276331 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TW | LD16TW | ld1 6tw | ld16tw | Powys | Powys | Llanbister STW | 2321 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 311767 | 271456 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6TY | LD16TY | ld1 6ty | ld16ty | Powys | Powys | Llanbadarn Ffynydd STW | 1489 | 1169 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.79 | 11.62 | 12.84 | 311268 | 277553 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6UA | LD16UA | ld1 6ua | ld16ua | Powys | Powys | Llanbadarn Ffynydd STW | 767 | 1169 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.79 | 11.62 | 12.84 | 309943 | 276979 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6UB | LD16UB | ld1 6ub | ld16ub | Powys | Powys | Llanbister STW | 2155 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 309826 | 275486 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6UD | LD16UD | ld1 6ud | ld16ud | Powys | Powys | Llanbister STW | 5608 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 316416 | 273485 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6UE | LD16UE | ld1 6ue | ld16ue | Powys | Powys | Llanbister STW | 4626 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 315434 | 273617 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6UF | LD16UF | ld1 6uf | ld16uf | Powys | Powys | Llanbister STW | 3943 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 314730 | 273985 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6UG | LD16UG | ld1 6ug | ld16ug | Powys | Powys | Llanbister STW | 4222 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 314709 | 275185 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6UH | LD16UH | ld1 6uh | ld16uh | Powys | Powys | Llanbister STW | 3110 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 313790 | 274458 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6UL | LD16UL | ld1 6ul | ld16ul | Powys | Powys | Llanbister STW | 1484 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 311607 | 274821 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6UN | LD16UN | ld1 6un | ld16un | Powys | Powys | Llanbadarn Ffynydd STW | 2203 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 311646 | 276544 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6UP | LD16UP | ld1 6up | ld16up | Powys | Powys | Llandewi Ystradenny STW | 3613 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 314000 | 267102 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6UR | LD16UR | ld1 6ur | ld16ur | Powys | Powys | Llandewi Ystradenny STW | 1945 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 311682 | 266589 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6UT | LD16UT | ld1 6ut | ld16ut | Powys | Powys | Penybont STW | 1628 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 311445 | 265489 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YA | LD16YA | ld1 6ya | ld16ya | Powys | Powys | Llanbadarn Ffynydd STW | 410 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 309834 | 278138 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YB | LD16YB | ld1 6yb | ld16yb | Powys | Powys | Llanbadarn Ffynydd STW | 1569 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 309457 | 279263 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YD | LD16YD | ld1 6yd | ld16yd | Powys | Powys | Llanbadarn Ffynydd STW | 2083 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 310299 | 279749 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YE | LD16YE | ld1 6ye | ld16ye | Powys | Powys | Llanbadarn Ffynydd STW | 4197 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 310528 | 281860 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YF | LD16YF | ld1 6yf | ld16yf | Powys | Powys | Llanbadarn Ffynydd STW | 2472 | 1152 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.47 | 11.45 | 12.66 | 311259 | 279717 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YG | LD16YG | ld1 6yg | ld16yg | Powys | Powys | Llanbadarn Ffynydd STW | 2612 | 1155 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.53 | 11.48 | 12.69 | 312268 | 278553 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YH | LD16YH | ld1 6yh | ld16yh | Powys | Powys | Llanbadarn Ffynydd STW | 50 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 309740 | 277735 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YL | LD16YL | ld1 6yl | ld16yl | Powys | Powys | Llanbadarn Ffynydd STW | 1415 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 308609 | 278509 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YN | LD16YN | ld1 6yn | ld16yn | Powys | Powys | Llanbadarn Ffynydd STW | 2682 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 307669 | 279371 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YP | LD16YP | ld1 6yp | ld16yp | Powys | Powys | Llanbadarn Ffynydd STW | 3346 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 306462 | 278066 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YR | LD16YR | ld1 6yr | ld16yr | Powys | Powys | Llanbadarn Ffynydd STW | 4267 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 305531 | 277978 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YS | LD16YS | ld1 6ys | ld16ys | Powys | Powys | Llanbadarn Ffynydd STW | 4765 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 306957 | 281560 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YT | LD16YT | ld1 6yt | ld16yt | Powys | Powys | Llanbadarn Ffynydd STW | 3092 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 308556 | 280564 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 6YW | LD16YW | ld1 6yw | ld16yw | Powys | Powys | Llanbadarn Ffynydd STW | 2807 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 307256 | 276524 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9AQ | LD19AQ | ld1 9aq | ld19aq | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9AY | LD19AY | ld1 9ay | ld19ay | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9BE | LD19BE | ld1 9be | ld19be | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9BL | LD19BL | ld1 9bl | ld19bl | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9BU | LD19BU | ld1 9bu | ld19bu | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9BW | LD19BW | ld1 9bw | ld19bw | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9BZ | LD19BZ | ld1 9bz | ld19bz | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9DA | LD19DA | ld1 9da | ld19da | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9SA | LD19SA | ld1 9sa | ld19sa | Powys | Powys | Llandrindod Wells STW | 1473 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306339 | 260844 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9SB | LD19SB | ld1 9sb | ld19sb | Powys | Powys | Llandrindod Wells STW | 1473 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306339 | 260844 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9XF | LD19XF | ld1 9xf | ld19xf | Powys | Powys | Llandrindod Wells STW | 1473 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306339 | 260844 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9ZX | LD19ZX | ld1 9zx | ld19zx | Powys | Powys | Llandrindod Wells STW | 1473 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306339 | 260844 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9ZY | LD19ZY | ld1 9zy | ld19zy | Powys | Powys | Llandrindod Wells STW | 1473 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306339 | 260844 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD1 9ZZ | LD19ZZ | ld1 9zz | ld19zz | Powys | Powys | Llandrindod Wells STW | 1473 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 306339 | 260844 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AA | LD23AA | ld2 3aa | ld23aa | Powys | Powys | Builth Wells STW | 675 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304071 | 250997 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AB | LD23AB | ld2 3ab | ld23ab | Powys | Powys | Builth Wells STW | 692 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304095 | 250951 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AD | LD23AD | ld2 3ad | ld23ad | Powys | Powys | Builth Wells STW | 714 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304081 | 250935 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AE | LD23AE | ld2 3ae | ld23ae | Powys | Powys | Builth Wells STW | 517 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304223 | 251072 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AG | LD23AG | ld2 3ag | ld23ag | Powys | Powys | Builth Wells STW | 733 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304073 | 250916 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AH | LD23AH | ld2 3ah | ld23ah | Powys | Powys | Builth Wells STW | 750 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304026 | 250937 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AJ | LD23AJ | ld2 3aj | ld23aj | Powys | Powys | Erwood STW | 3255 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 308125 | 240630 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AL | LD23AL | ld2 3al | ld23al | Powys | Powys | Builth Wells STW | 811 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303922 | 250960 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AN | LD23AN | ld2 3an | ld23an | Powys | Powys | Builth Wells STW | 828 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303975 | 250877 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AP | LD23AP | ld2 3ap | ld23ap | Powys | Powys | Builth Wells STW | 804 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303879 | 251032 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AQ | LD23AQ | ld2 3aq | ld23aq | Powys | Powys | Erwood STW | 1922 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 309723 | 241389 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AR | LD23AR | ld2 3ar | ld23ar | Powys | Powys | Builth Wells STW | 899 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303761 | 251044 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AS | LD23AS | ld2 3as | ld23as | Powys | Powys | Builth Wells STW | 1053 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303564 | 251108 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AT | LD23AT | ld2 3at | ld23at | Powys | Powys | Builth Wells STW | 917 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303802 | 250944 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AU | LD23AU | ld2 3au | ld23au | Powys | Powys | Builth Wells STW | 932 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303677 | 251150 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AW | LD23AW | ld2 3aw | ld23aw | Powys | Powys | Builth Wells STW | 923 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303956 | 250767 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AX | LD23AX | ld2 3ax | ld23ax | Powys | Powys | Gwenddwr STW | 4524 | 1133 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.12 | 11.26 | 12.45 | 307820 | 239130 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AY | LD23AY | ld2 3ay | ld23ay | Powys | Powys | Builth Wells STW | 843 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303789 | 251112 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3AZ | LD23AZ | ld2 3az | ld23az | Powys | Powys | Erwood STW | 4248 | 1133 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.12 | 11.26 | 12.45 | 308087 | 239498 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BA | LD23BA | ld2 3ba | ld23ba | Powys | Powys | Builth Wells STW | 804 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303834 | 251109 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BB | LD23BB | ld2 3bb | ld23bb | Powys | Powys | Builth Wells STW | 656 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304154 | 250950 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BD | LD23BD | ld2 3bd | ld23bd | Powys | Powys | Builth Wells STW | 625 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304113 | 251027 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BE | LD23BE | ld2 3be | ld23be | Powys | Powys | Builth Wells STW | 943 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303864 | 250826 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BF | LD23BF | ld2 3bf | ld23bf | Powys | Powys | Builth Wells STW | 419 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304540 | 251052 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BG | LD23BG | ld2 3bg | ld23bg | Powys | Powys | Builth Wells STW | 665 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304038 | 251050 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BH | LD23BH | ld2 3bh | ld23bh | Powys | Powys | Builth Wells STW | 633 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304075 | 251055 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BJ | LD23BJ | ld2 3bj | ld23bj | Powys | Powys | STW At Lower Chapel Brecon , | 4418 | 1195 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.27 | 11.88 | 13.13 | 306018 | 238690 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BL | LD23BL | ld2 3bl | ld23bl | Powys | Powys | Builth Wells STW | 542 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304188 | 251069 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BN | LD23BN | ld2 3bn | ld23bn | Powys | Powys | Builth Wells STW | 408 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304348 | 251118 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BP | LD23BP | ld2 3bp | ld23bp | Powys | Powys | Builth Wells STW | 324 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304614 | 251153 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BQ | LD23BQ | ld2 3bq | ld23bq | Powys | Powys | Gwenddwr STW | 4288 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 306586 | 239121 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BS | LD23BS | ld2 3bs | ld23bs | Powys | Powys | Builth Wells STW | 693 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303981 | 251078 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BT | LD23BT | ld2 3bt | ld23bt | Powys | Powys | Builth Wells STW | 686 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303958 | 251129 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BU | LD23BU | ld2 3bu | ld23bu | Powys | Powys | Builth Wells STW | 798 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303773 | 251300 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BW | LD23BW | ld2 3bw | ld23bw | Powys | Powys | Builth Wells STW | 774 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303807 | 251261 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BX | LD23BX | ld2 3bx | ld23bx | Powys | Powys | Gwenddwr STW | 2347 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 307753 | 241534 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BY | LD23BY | ld2 3by | ld23by | Powys | Powys | Builth Wells STW | 1208 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303370 | 251221 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3BZ | LD23BZ | ld2 3bz | ld23bz | Powys | Powys | Gwenddwr STW | 1339 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 307223 | 244397 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DA | LD23DA | ld2 3da | ld23da | Powys | Powys | Builth Wells STW | 1200 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303372 | 251255 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DB | LD23DB | ld2 3db | ld23db | Powys | Powys | Builth Wells STW | 1014 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303577 | 251192 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DD | LD23DD | ld2 3dd | ld23dd | Powys | Powys | Builth Wells STW | 928 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303627 | 251401 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DE | LD23DE | ld2 3de | ld23de | Powys | Powys | Builth Wells STW | 1119 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303479 | 251153 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DF | LD23DF | ld2 3df | ld23df | Powys | Powys | Builth Wells STW | 1342 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303262 | 251103 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DG | LD23DG | ld2 3dg | ld23dg | Powys | Powys | Builth Wells STW | 1227 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303333 | 251336 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DH | LD23DH | ld2 3dh | ld23dh | Powys | Powys | Builth Wells STW | 774 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304220 | 250772 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DJ | LD23DJ | ld2 3dj | ld23dj | Powys | Powys | Builth Wells STW | 356 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304383 | 251158 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DL | LD23DL | ld2 3dl | ld23dl | Powys | Powys | Builth Wells STW | 626 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304132 | 251007 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DN | LD23DN | ld2 3dn | ld23dn | Powys | Powys | Builth Wells STW | 557 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304193 | 251045 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DP | LD23DP | ld2 3dp | ld23dp | Powys | Powys | Builth Wells STW | 547 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304231 | 251028 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DQ | LD23DQ | ld2 3dq | ld23dq | Powys | Powys | Builth Wells STW | 859 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304543 | 250612 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DR | LD23DR | ld2 3dr | ld23dr | Powys | Powys | Builth Wells STW | 537 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304251 | 251027 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DS | LD23DS | ld2 3ds | ld23ds | Powys | Powys | Builth Wells STW | 574 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304239 | 250990 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DT | LD23DT | ld2 3dt | ld23dt | Powys | Powys | Builth Wells STW | 515 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304245 | 251058 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DU | LD23DU | ld2 3du | ld23du | Powys | Powys | Builth Wells STW | 509 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304272 | 251046 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DW | LD23DW | ld2 3dw | ld23dw | Powys | Powys | Builth Wells STW | 592 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304148 | 251039 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DX | LD23DX | ld2 3dx | ld23dx | Powys | Powys | Builth Wells STW | 656 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304338 | 250851 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DY | LD23DY | ld2 3dy | ld23dy | Powys | Powys | Builth Wells STW | 1073 | 1111 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.71 | 11.04 | 12.21 | 304237 | 250446 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3DZ | LD23DZ | ld2 3dz | ld23dz | Powys | Powys | Builth Wells STW | 1053 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303564 | 251108 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EA | LD23EA | ld2 3ea | ld23ea | Powys | Powys | Builth Wells STW | 711 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304115 | 250911 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EB | LD23EB | ld2 3eb | ld23eb | Powys | Powys | Builth Wells STW | 820 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304120 | 250774 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3ED | LD23ED | ld2 3ed | ld23ed | Powys | Powys | Builth Wells STW | 720 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304142 | 250879 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EE | LD23EE | ld2 3ee | ld23ee | Powys | Powys | Builth Wells STW | 826 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304167 | 250740 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EF | LD23EF | ld2 3ef | ld23ef | Powys | Powys | Builth Wells STW | 664 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304192 | 250913 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EG | LD23EG | ld2 3eg | ld23eg | Powys | Powys | Builth Wells STW | 578 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304329 | 250938 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EH | LD23EH | ld2 3eh | ld23eh | Powys | Powys | Builth Wells STW | 595 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304446 | 250886 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EJ | LD23EJ | ld2 3ej | ld23ej | Powys | Powys | Erwood STW | 427 | 1008 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.79 | 10.02 | 11.07 | 309665 | 243026 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EL | LD23EL | ld2 3el | ld23el | Powys | Powys | Builth Wells STW | 487 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304481 | 250989 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EN | LD23EN | ld2 3en | ld23en | Powys | Powys | Builth Wells STW | 412 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304608 | 251063 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EP | LD23EP | ld2 3ep | ld23ep | Powys | Powys | Builth Wells STW | 550 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304556 | 250921 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EQ | LD23EQ | ld2 3eq | ld23eq | Powys | Powys | Erwood STW | 510 | 1008 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.79 | 10.02 | 11.07 | 309534 | 243082 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3ER | LD23ER | ld2 3er | ld23er | Powys | Powys | Builth Wells STW | 367 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304746 | 251160 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3ES | LD23ES | ld2 3es | ld23es | Powys | Powys | Builth Wells STW | 390 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304604 | 251085 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3ET | LD23ET | ld2 3et | ld23et | Powys | Powys | Builth Wells STW | 366 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304613 | 251110 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EU | LD23EU | ld2 3eu | ld23eu | Powys | Powys | Builth Wells STW | 377 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304610 | 251099 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EW | LD23EW | ld2 3ew | ld23ew | Powys | Powys | Builth Wells STW | 362 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304644 | 251121 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EX | LD23EX | ld2 3ex | ld23ex | Powys | Powys | Erwood STW | 400 | 1008 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.79 | 10.02 | 11.07 | 309720 | 243005 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EY | LD23EY | ld2 3ey | ld23ey | Powys | Powys | Builth Wells STW | 357 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304622 | 251121 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3EZ | LD23EZ | ld2 3ez | ld23ez | Powys | Powys | Erwood STW | 381 | 1008 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.79 | 10.02 | 11.07 | 309677 | 243088 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3FA | LD23FA | ld2 3fa | ld23fa | Powys | Powys | Cilmery STW | 698 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 300168 | 251505 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3FD | LD23FD | ld2 3fd | ld23fd | Powys | Powys | Builth Wells STW | 1043 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303890 | 250665 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3FE | LD23FE | ld2 3fe | ld23fe | Powys | Powys | Builth Wells STW | 715 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304355 | 250784 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3FF | LD23FF | ld2 3ff | ld23ff | Powys | Powys | Aberedw STW | 302 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 307901 | 247417 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3FL | LD23FL | ld2 3fl | ld23fl | Powys | Powys | Cilmery STW | 328 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 300771 | 251473 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3GA | LD23GA | ld2 3ga | ld23ga | Powys | Powys | Builth Wells STW | 1085 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303694 | 250807 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3GE | LD23GE | ld2 3ge | ld23ge | Powys | Powys | Cilmery STW | 590 | 1268 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.63 | 12.6 | 13.93 | 300325 | 251450 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3GF | LD23GF | ld2 3gf | ld23gf | Powys | Powys | Builth Wells STW | 651 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304285 | 250878 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3GG | LD23GG | ld2 3gg | ld23gg | Powys | Powys | Builth Wells STW | 775 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304120 | 250828 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HA | LD23HA | ld2 3ha | ld23ha | Powys | Powys | Builth Wells STW | 982 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303711 | 250965 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HB | LD23HB | ld2 3hb | ld23hb | Powys | Powys | Builth Wells STW | 376 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304677 | 251117 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HD | LD23HD | ld2 3hd | ld23hd | Powys | Powys | Builth Wells STW | 2964 | 1195 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.27 | 11.88 | 13.13 | 302862 | 249037 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HE | LD23HE | ld2 3he | ld23he | Powys | Powys | Builth Wells STW | 1215 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303521 | 250829 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HF | LD23HF | ld2 3hf | ld23hf | Powys | Powys | Builth Wells STW | 1474 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303241 | 250799 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HG | LD23HG | ld2 3hg | ld23hg | Powys | Powys | Builth Wells STW | 1603 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303194 | 250620 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HH | LD23HH | ld2 3hh | ld23hh | Powys | Powys | Cilmery STW | 2221 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 302198 | 250075 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HJ | LD23HJ | ld2 3hj | ld23hj | Powys | Powys | Gwenddwr STW | 1392 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 305509 | 242277 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HL | LD23HL | ld2 3hl | ld23hl | Powys | Powys | Cilmery STW | 2595 | 1320 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.6 | 13.12 | 14.5 | 300341 | 249247 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HN | LD23HN | ld2 3hn | ld23hn | Powys | Powys | Cilmery STW | 1897 | 1245 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.2 | 12.38 | 13.68 | 300063 | 250053 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HP | LD23HP | ld2 3hp | ld23hp | Powys | Powys | Builth Wells STW | 2526 | 1134 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.14 | 11.27 | 12.46 | 302729 | 249724 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HQ | LD23HQ | ld2 3hq | ld23hq | Powys | Powys | Gwenddwr STW | 197 | 1161 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.64 | 11.54 | 12.76 | 306495 | 243293 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HR | LD23HR | ld2 3hr | ld23hr | Powys | Powys | Builth Wells STW | 2563 | 1121 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.89 | 11.14 | 12.32 | 303548 | 249114 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HS | LD23HS | ld2 3hs | ld23hs | Powys | Powys | Cilmery STW | 4517 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 301656 | 247366 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HT | LD23HT | ld2 3ht | ld23ht | Powys | Powys | Cilmery STW | 4461 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 300109 | 247394 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HU | LD23HU | ld2 3hu | ld23hu | Powys | Powys | Gwenddwr STW | 5766 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 301195 | 246019 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HW | LD23HW | ld2 3hw | ld23hw | Powys | Powys | Garth STW | 3133 | 1367 | 1200to1500 | 2.74 | 2 | 1.47 | 25.48 | 13.59 | 15.02 | 298332 | 249433 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HX | LD23HX | ld2 3hx | ld23hx | Powys | Powys | Gwenddwr STW | 1435 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 304897 | 243477 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HY | LD23HY | ld2 3hy | ld23hy | Powys | Powys | Gwenddwr STW | 4370 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 302046 | 244255 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3HZ | LD23HZ | ld2 3hz | ld23hz | Powys | Powys | Gwenddwr STW | 1163 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 306104 | 244540 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JB | LD23JB | ld2 3jb | ld23jb | Powys | Powys | Painscastle STW | 2256 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 318860 | 247711 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JD | LD23JD | ld2 3jd | ld23jd | Powys | Powys | Painscastle STW | 2479 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 318827 | 248077 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JE | LD23JE | ld2 3je | ld23je | Powys | Powys | Erwood STW | 1149 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 309877 | 244432 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JF | LD23JF | ld2 3jf | ld23jf | Powys | Powys | Erwood STW | 2038 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 311218 | 244923 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JG | LD23JG | ld2 3jg | ld23jg | Powys | Powys | Erwood STW | 2742 | 1020 | 900to1200 | 2.04 | 1.49 | 1.1 | 19.01 | 10.14 | 11.21 | 312085 | 245069 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JH | LD23JH | ld2 3jh | ld23jh | Powys | Powys | Painscastle STW | 2938 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 314169 | 246489 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JJ | LD23JJ | ld2 3jj | ld23jj | Powys | Powys | Painscastle STW | 1305 | 1047 | 900to1200 | 2.1 | 1.53 | 1.12 | 19.51 | 10.41 | 11.5 | 315805 | 246456 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JL | LD23JL | ld2 3jl | ld23jl | Powys | Powys | Painscastle STW | 366 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 316734 | 246289 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JN | LD23JN | ld2 3jn | ld23jn | Powys | Powys | Painscastle STW | 1585 | 1032 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.23 | 10.26 | 11.34 | 316191 | 245002 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JP | LD23JP | ld2 3jp | ld23jp | Powys | Powys | Painscastle STW | 1096 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 318190 | 246190 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JQ | LD23JQ | ld2 3jq | ld23jq | Powys | Powys | Erwood STW | 3763 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 312954 | 245619 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JR | LD23JR | ld2 3jr | ld23jr | Powys | Powys | Painscastle STW | 1385 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 318447 | 246621 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JS | LD23JS | ld2 3js | ld23js | Powys | Powys | Painscastle STW | 1251 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 317965 | 247203 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JT | LD23JT | ld2 3jt | ld23jt | Powys | Powys | Painscastle STW | 2146 | 1104 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.58 | 10.97 | 12.13 | 316907 | 248437 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JU | LD23JU | ld2 3ju | ld23ju | Powys | Powys | Painscastle STW | 2440 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 318827 | 248023 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JW | LD23JW | ld2 3jw | ld23jw | Powys | Powys | Painscastle STW | 1382 | 1013 | 900to1200 | 2.03 | 1.48 | 1.09 | 18.88 | 10.07 | 11.13 | 318060 | 245307 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JX | LD23JX | ld2 3jx | ld23jx | Powys | Powys | Painscastle STW | 380 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 316766 | 246118 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JY | LD23JY | ld2 3jy | ld23jy | Powys | Powys | Painscastle STW | 2153 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 318822 | 247591 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3JZ | LD23JZ | ld2 3jz | ld23jz | Powys | Powys | Painscastle STW | 260 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 316859 | 246203 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LA | LD23LA | ld2 3la | ld23la | Powys | Powys | Cilmery STW | 4936 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 302223 | 247075 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LB | LD23LB | ld2 3lb | ld23lb | Powys | Powys | Builth Wells STW | 1824 | 1111 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.71 | 11.04 | 12.21 | 303987 | 249737 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LD | LD23LD | ld2 3ld | ld23ld | Powys | Powys | Builth Wells STW | 1539 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303211 | 250717 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LE | LD23LE | ld2 3le | ld23le | Powys | Powys | Builth Wells STW | 1371 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303346 | 250820 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LF | LD23LF | ld2 3lf | ld23lf | Powys | Powys | Builth Wells STW | 961 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304104 | 250621 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LG | LD23LG | ld2 3lg | ld23lg | Powys | Powys | Cilmery STW | 1176 | 1268 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.63 | 12.6 | 13.93 | 299772 | 251229 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LH | LD23LH | ld2 3lh | ld23lh | Powys | Powys | Cilmery STW | 2316 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 298847 | 250557 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LJ | LD23LJ | ld2 3lj | ld23lj | Powys | Powys | Aberedw STW | 1384 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 306328 | 246855 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LN | LD23LN | ld2 3ln | ld23ln | Powys | Powys | Garth STW | 2115 | 1342 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.01 | 13.34 | 14.74 | 294902 | 251493 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LP | LD23LP | ld2 3lp | ld23lp | Powys | Powys | Beulah STW | 2779 | 1618 | Over1500 | 3.24 | 2.37 | 1.74 | 30.16 | 16.08 | 17.78 | 293406 | 253552 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LQ | LD23LQ | ld2 3lq | ld23lq | Powys | Powys | Aberedw STW | 1675 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 306638 | 246029 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LR | LD23LR | ld2 3lr | ld23lr | Powys | Powys | Beulah STW | 2073 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 294194 | 251673 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LS | LD23LS | ld2 3ls | ld23ls | Powys | Powys | Beulah STW | 2782 | 1731 | Over1500 | 3.46 | 2.54 | 1.86 | 32.26 | 17.21 | 19.02 | 292087 | 253817 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LT | LD23LT | ld2 3lt | ld23lt | Powys | Powys | Beulah STW | 3398 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 294558 | 253505 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LU | LD23LU | ld2 3lu | ld23lu | Powys | Powys | Beulah STW | 3850 | 1675 | Over1500 | 3.35 | 2.45 | 1.8 | 31.22 | 16.65 | 18.4 | 293570 | 254644 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LW | LD23LW | ld2 3lw | ld23lw | Powys | Powys | Beulah STW | 3044 | 1494 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.85 | 14.85 | 16.41 | 294420 | 253142 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LX | LD23LX | ld2 3lx | ld23lx | Powys | Powys | Aberedw STW | 1800 | 1138 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.21 | 11.31 | 12.5 | 306055 | 248322 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LY | LD23LY | ld2 3ly | ld23ly | Powys | Powys | Beulah STW | 3935 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 294294 | 254383 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3LZ | LD23LZ | ld2 3lz | ld23lz | Powys | Powys | Builth Wells STW | 1493 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 304641 | 249981 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NA | LD23NA | ld2 3na | ld23na | Powys | Powys | Beulah STW | 3889 | 1379 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.7 | 13.71 | 15.15 | 295348 | 253349 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NB | LD23NB | ld2 3nb | ld23nb | Powys | Powys | Garth STW | 5202 | 1515 | Over1500 | 3.03 | 2.22 | 1.63 | 28.24 | 15.06 | 16.65 | 296092 | 254524 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3ND | LD23ND | ld2 3nd | ld23nd | Powys | Powys | Cilmery STW | 4724 | 1288 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.01 | 12.8 | 14.15 | 297586 | 255261 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NE | LD23NE | ld2 3ne | ld23ne | Powys | Powys | Cilmery STW | 3436 | 1220 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.74 | 12.13 | 13.4 | 297984 | 253767 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NF | LD23NF | ld2 3nf | ld23nf | Powys | Powys | Builth Wells STW | 1288 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 303265 | 251516 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NG | LD23NG | ld2 3ng | ld23ng | Powys | Powys | Builth Wells STW | 1412 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 303155 | 251670 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NH | LD23NH | ld2 3nh | ld23nh | Powys | Powys | Builth Wells STW | 1204 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303403 | 251111 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NJ | LD23NJ | ld2 3nj | ld23nj | Powys | Powys | Builth Wells STW | 867 | 1059 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.74 | 10.53 | 11.64 | 303903 | 252046 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NL | LD23NL | ld2 3nl | ld23nl | Powys | Powys | Builth Wells STW | 1283 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303349 | 251027 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NN | LD23NN | ld2 3nn | ld23nn | Powys | Powys | Builth Wells STW | 1397 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303179 | 251218 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NP | LD23NP | ld2 3np | ld23np | Powys | Powys | Builth Wells STW | 1640 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303046 | 250824 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NQ | LD23NQ | ld2 3nq | ld23nq | Powys | Powys | Builth Wells STW | 2256 | 1119 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.86 | 11.12 | 12.29 | 304782 | 249227 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NR | LD23NR | ld2 3nr | ld23nr | Powys | Powys | Builth Road STW | 1831 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 302644 | 251330 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NS | LD23NS | ld2 3ns | ld23ns | Powys | Powys | Cilmery STW | 1740 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 302369 | 251048 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NT | LD23NT | ld2 3nt | ld23nt | Powys | Powys | Cilmery STW | 182 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 300967 | 251729 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NU | LD23NU | ld2 3nu | ld23nu | Powys | Powys | Cilmery STW | 652 | 1268 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.63 | 12.6 | 13.93 | 300313 | 251367 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NW | LD23NW | ld2 3nw | ld23nw | Powys | Powys | Builth Road STW | 1258 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 302716 | 251972 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NX | LD23NX | ld2 3nx | ld23nx | Powys | Powys | Builth Wells STW | 1053 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303654 | 250922 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NY | LD23NY | ld2 3ny | ld23ny | Powys | Powys | Cilmery STW | 543 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 300315 | 251556 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3NZ | LD23NZ | ld2 3nz | ld23nz | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PA | LD23PA | ld2 3pa | ld23pa | Powys | Powys | Cilmery STW | 623 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 300213 | 251591 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PB | LD23PB | ld2 3pb | ld23pb | Powys | Powys | Cilmery STW | 1114 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 299700 | 251976 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PD | LD23PD | ld2 3pd | ld23pd | Powys | Powys | Cilmery STW | 3156 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 298066 | 253375 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PE | LD23PE | ld2 3pe | ld23pe | Powys | Powys | Cilmery STW | 4416 | 1368 | 1200to1500 | 2.74 | 2 | 1.47 | 25.5 | 13.6 | 15.03 | 296816 | 253701 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PF | LD23PF | ld2 3pf | ld23pf | Powys | Powys | Beulah STW | 5626 | 1515 | Over1500 | 3.03 | 2.22 | 1.63 | 28.24 | 15.06 | 16.65 | 296006 | 255199 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PG | LD23PG | ld2 3pg | ld23pg | Powys | Powys | Beulah STW | 5824 | 1661 | Over1500 | 3.32 | 2.43 | 1.78 | 30.96 | 16.51 | 18.25 | 295457 | 255880 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PH | LD23PH | ld2 3ph | ld23ph | Powys | Powys | Beulah STW | 4797 | 1675 | Over1500 | 3.35 | 2.45 | 1.8 | 31.22 | 16.65 | 18.4 | 293991 | 255496 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PJ | LD23PJ | ld2 3pj | ld23pj | Powys | Powys | Erwood STW | 1413 | 1048 | 900to1200 | 2.1 | 1.53 | 1.13 | 19.53 | 10.42 | 11.51 | 309040 | 242254 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PL | LD23PL | ld2 3pl | ld23pl | Powys | Powys | Llanwrthwl STW | 6665 | 1735 | Over1500 | 3.47 | 2.54 | 1.86 | 32.34 | 17.25 | 19.06 | 294549 | 257511 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PN | LD23PN | ld2 3pn | ld23pn | Powys | Powys | Newbridge-On-Wye STW | 5323 | 1472 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.44 | 14.63 | 16.17 | 296716 | 255729 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PP | LD23PP | ld2 3pp | ld23pp | Powys | Powys | Cilmery STW | 3611 | 1211 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.57 | 12.04 | 13.31 | 298891 | 254864 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PQ | LD23PQ | ld2 3pq | ld23pq | Powys | Powys | Erwood STW | 455 | 1008 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.79 | 10.02 | 11.07 | 309858 | 242858 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PR | LD23PR | ld2 3pr | ld23pr | Powys | Powys | Builth Road STW | 3496 | 1211 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.57 | 12.04 | 13.31 | 299182 | 254951 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PS | LD23PS | ld2 3ps | ld23ps | Powys | Powys | Cilmery STW | 2558 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 299442 | 253967 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PT | LD23PT | ld2 3pt | ld23pt | Powys | Powys | Cilmery STW | 718 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 301110 | 252447 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PU | LD23PU | ld2 3pu | ld23pu | Powys | Powys | Builth Road STW | 625 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 302182 | 252467 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PW | LD23PW | ld2 3pw | ld23pw | Powys | Powys | Newbridge-On-Wye STW | 4725 | 1517 | Over1500 | 3.04 | 2.22 | 1.63 | 28.27 | 15.08 | 16.67 | 296990 | 256622 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PX | LD23PX | ld2 3px | ld23px | Powys | Powys | Erwood STW | 2063 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 308154 | 242370 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PY | LD23PY | ld2 3py | ld23py | Powys | Powys | Builth Road STW | 402 | 1120 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.88 | 11.13 | 12.31 | 302501 | 253267 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3PZ | LD23PZ | ld2 3pz | ld23pz | Powys | Powys | Gwenddwr STW | 927 | 1127 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.01 | 11.2 | 12.38 | 307097 | 242879 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RA | LD23RA | ld2 3ra | ld23ra | Powys | Powys | Builth Road STW | 1519 | 1148 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.4 | 11.41 | 12.61 | 301479 | 254457 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RB | LD23RB | ld2 3rb | ld23rb | Powys | Powys | Builth Road STW | 1555 | 1102 | 900to1200 | 2.21 | 1.61 | 1.18 | 20.54 | 10.95 | 12.11 | 301498 | 254506 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RD | LD23RD | ld2 3rd | ld23rd | Powys | Powys | Builth Road STW | 1216 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 303131 | 252386 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RE | LD23RE | ld2 3re | ld23re | Powys | Powys | Builth Wells STW | 1436 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303356 | 250677 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RF | LD23RF | ld2 3rf | ld23rf | Powys | Powys | Builth Road STW | 745 | 1120 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.88 | 11.13 | 12.31 | 302869 | 253243 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RG | LD23RG | ld2 3rg | ld23rg | Powys | Powys | Builth Road STW | 426 | 1120 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.88 | 11.13 | 12.31 | 302565 | 253118 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RH | LD23RH | ld2 3rh | ld23rh | Powys | Powys | Builth Road STW | 429 | 1146 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.36 | 11.39 | 12.59 | 302484 | 253346 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RJ | LD23RJ | ld2 3rj | ld23rj | Powys | Powys | Builth Wells STW | 3776 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 303309 | 247907 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RL | LD23RL | ld2 3rl | ld23rl | Powys | Powys | Builth Road STW | 260 | 1146 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.36 | 11.39 | 12.59 | 302312 | 253285 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RN | LD23RN | ld2 3rn | ld23rn | Powys | Powys | Builth Road STW | 841 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 302830 | 253570 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RP | LD23RP | ld2 3rp | ld23rp | Powys | Powys | Builth Road STW | 1923 | 1102 | 900to1200 | 2.21 | 1.61 | 1.18 | 20.54 | 10.95 | 12.11 | 300913 | 254570 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RQ | LD23RQ | ld2 3rq | ld23rq | Powys | Powys | Gwenddwr STW | 4701 | 1277 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.8 | 12.69 | 14.03 | 302791 | 246492 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RR | LD23RR | ld2 3rr | ld23rr | Powys | Powys | Builth Road STW | 1600 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 301503 | 254557 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RS | LD23RS | ld2 3rs | ld23rs | Powys | Powys | Builth Road STW | 1809 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 302375 | 254883 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RT | LD23RT | ld2 3rt | ld23rt | Powys | Powys | Builth Road STW | 2248 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 302180 | 255337 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RU | LD23RU | ld2 3ru | ld23ru | Powys | Powys | Newbridge-On-Wye STW | 2119 | 1117 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.82 | 11.1 | 12.27 | 301702 | 256014 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RW | LD23RW | ld2 3rw | ld23rw | Powys | Powys | Builth Road STW | 1270 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 302856 | 254138 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RX | LD23RX | ld2 3rx | ld23rx | Powys | Powys | Builth Wells STW | 3009 | 1121 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.89 | 11.14 | 12.32 | 303546 | 248636 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RY | LD23RY | ld2 3ry | ld23ry | Powys | Powys | Newbridge-On-Wye STW | 1471 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 302111 | 256796 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3RZ | LD23RZ | ld2 3rz | ld23rz | Powys | Powys | Builth Wells STW | 2769 | 1121 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.89 | 11.14 | 12.32 | 304451 | 248705 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SA | LD23SA | ld2 3sa | ld23sa | Powys | Powys | Newbridge-On-Wye STW | 917 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 302196 | 257561 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SB | LD23SB | ld2 3sb | ld23sb | Powys | Powys | Newbridge-On-Wye STW | 613 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 301686 | 257547 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SD | LD23SD | ld2 3sd | ld23sd | Powys | Powys | Newbridge-On-Wye STW | 641 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 301129 | 257578 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SE | LD23SE | ld2 3se | ld23se | Powys | Powys | Newbridge-On-Wye STW | 2211 | 1242 | 1200to1500 | 2.49 | 1.82 | 1.33 | 23.15 | 12.35 | 13.65 | 300328 | 256227 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SF | LD23SF | ld2 3sf | ld23sf | Powys | Powys | Builth Road STW | 3132 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 299531 | 254822 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SG | LD23SG | ld2 3sg | ld23sg | Powys | Powys | Newbridge-On-Wye STW | 3893 | 1499 | 1200to1500 | 3 | 2.2 | 1.61 | 27.94 | 14.9 | 16.47 | 297584 | 257900 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SH | LD23SH | ld2 3sh | ld23sh | Powys | Powys | Newbridge-On-Wye STW | 2770 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 299003 | 256861 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SJ | LD23SJ | ld2 3sj | ld23sj | Powys | Powys | Erwood STW | 1130 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 309080 | 243945 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SL | LD23SL | ld2 3sl | ld23sl | Powys | Powys | Newbridge-On-Wye STW | 1528 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 300129 | 257388 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SN | LD23SN | ld2 3sn | ld23sn | Powys | Powys | Builth Road STW | 1661 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 301515 | 254628 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SP | LD23SP | ld2 3sp | ld23sp | Powys | Powys | Builth Road STW | 1407 | 1174 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.88 | 11.67 | 12.9 | 301746 | 254440 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SQ | LD23SQ | ld2 3sq | ld23sq | Powys | Powys | Aberedw STW | 1710 | 1076 | 900to1200 | 2.15 | 1.58 | 1.16 | 20.05 | 10.7 | 11.82 | 307668 | 245692 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SR | LD23SR | ld2 3sr | ld23sr | Powys | Powys | Builth Wells STW | 402 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304169 | 251350 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SS | LD23SS | ld2 3ss | ld23ss | Powys | Powys | Builth Wells STW | 367 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 304190 | 251413 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3ST | LD23ST | ld2 3st | ld23st | Powys | Powys | Builth Wells STW | 650 | 1059 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.74 | 10.53 | 11.64 | 303905 | 251535 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SU | LD23SU | ld2 3su | ld23su | Powys | Powys | Builth Wells STW | 593 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 303960 | 251498 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SW | LD23SW | ld2 3sw | ld23sw | Powys | Powys | Builth Road STW | 1630 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 301518 | 254596 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SX | LD23SX | ld2 3sx | ld23sx | Powys | Powys | Erwood STW | 999 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 310272 | 244251 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SY | LD23SY | ld2 3sy | ld23sy | Powys | Powys | Builth Wells STW | 739 | 1059 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.74 | 10.53 | 11.64 | 303932 | 251872 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3SZ | LD23SZ | ld2 3sz | ld23sz | Powys | Powys | Erwood STW | 1021 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 310528 | 242416 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TA | LD23TA | ld2 3ta | ld23ta | Powys | Powys | Builth Wells STW | 1067 | 1059 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.74 | 10.53 | 11.64 | 303644 | 252030 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TB | LD23TB | ld2 3tb | ld23tb | Powys | Powys | Builth Wells STW | 1598 | 1059 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.74 | 10.53 | 11.64 | 306097 | 251879 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TD | LD23TD | ld2 3td | ld23td | Powys | Powys | Llanfaredd STW | 2046 | 1067 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.89 | 10.61 | 11.72 | 306525 | 252469 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TE | LD23TE | ld2 3te | ld23te | Powys | Powys | Hundred House STW | 3152 | 1103 | 900to1200 | 2.21 | 1.62 | 1.18 | 20.56 | 10.96 | 12.12 | 308008 | 253502 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TF | LD23TF | ld2 3tf | ld23tf | Powys | Powys | Builth Wells STW | 2019 | 1080 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.13 | 10.74 | 11.87 | 304438 | 253486 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TG | LD23TG | ld2 3tg | ld23tg | Powys | Powys | Builth Wells STW | 2988 | 1095 | 900to1200 | 2.19 | 1.6 | 1.18 | 20.41 | 10.88 | 12.03 | 305266 | 254372 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TH | LD23TH | ld2 3th | ld23th | Powys | Powys | Builth Road STW | 2290 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303998 | 254427 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TJ | LD23TJ | ld2 3tj | ld23tj | Powys | Powys | Erwood STW | 3018 | 956 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.82 | 9.5 | 10.5 | 311890 | 240938 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TL | LD23TL | ld2 3tl | ld23tl | Powys | Powys | Llandrindod Wells STW | 4620 | 1129 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.04 | 11.22 | 12.4 | 305789 | 255966 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TN | LD23TN | ld2 3tn | ld23tn | Powys | Powys | Builth Road STW | 2527 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 303789 | 255004 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TP | LD23TP | ld2 3tp | ld23tp | Powys | Powys | Builth Wells STW | 604 | 1061 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.78 | 10.55 | 11.66 | 304854 | 251994 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TQ | LD23TQ | ld2 3tq | ld23tq | Powys | Powys | Erwood STW | 2371 | 1000 | 900to1200 | 2 | 1.46 | 1.07 | 18.64 | 9.94 | 10.99 | 311273 | 241290 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TR | LD23TR | ld2 3tr | ld23tr | Powys | Powys | Builth Wells STW | 429 | 1061 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.78 | 10.55 | 11.66 | 304602 | 251897 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TS | LD23TS | ld2 3ts | ld23ts | Powys | Powys | Builth Road STW | 1587 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 301560 | 254567 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TT | LD23TT | ld2 3tt | ld23tt | Powys | Powys | Builth Road STW | 1472 | 1174 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.88 | 11.67 | 12.9 | 301516 | 254423 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TU | LD23TU | ld2 3tu | ld23tu | Powys | Powys | Builth Wells STW | 841 | 1059 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.74 | 10.53 | 11.64 | 303859 | 251947 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TW | LD23TW | ld2 3tw | ld23tw | Powys | Powys | Newbridge-On-Wye STW | 2898 | 1191 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.2 | 11.84 | 13.09 | 303759 | 256344 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TX | LD23TX | ld2 3tx | ld23tx | Powys | Powys | Erwood STW | 2403 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 310006 | 240888 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TY | LD23TY | ld2 3ty | ld23ty | Powys | Powys | Builth Wells STW | 356 | 1061 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.78 | 10.55 | 11.66 | 304675 | 251805 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3TZ | LD23TZ | ld2 3tz | ld23tz | Powys | Powys | Erwood STW | 1678 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 311170 | 242088 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UA | LD23UA | ld2 3ua | ld23ua | Powys | Powys | Builth Wells STW | 562 | 1061 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.78 | 10.55 | 11.66 | 305002 | 251807 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UB | LD23UB | ld2 3ub | ld23ub | Powys | Powys | Builth Wells STW | 604 | 1061 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.78 | 10.55 | 11.66 | 304855 | 251993 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UD | LD23UD | ld2 3ud | ld23ud | Powys | Powys | Builth Wells STW | 1410 | 1059 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.74 | 10.53 | 11.64 | 305913 | 251837 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UE | LD23UE | ld2 3ue | ld23ue | Powys | Powys | Llanfaredd STW | 1584 | 1059 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.74 | 10.53 | 11.64 | 306232 | 251908 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UF | LD23UF | ld2 3uf | ld23uf | Powys | Powys | Llanfaredd STW | 958 | 1047 | 900to1200 | 2.1 | 1.53 | 1.12 | 19.51 | 10.41 | 11.5 | 306434 | 251313 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UG | LD23UG | ld2 3ug | ld23ug | Powys | Powys | Llanfaredd STW | 143 | 1115 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.78 | 11.08 | 12.25 | 306911 | 250321 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UH | LD23UH | ld2 3uh | ld23uh | Powys | Powys | Aberedw STW | 157 | 1045 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.48 | 10.39 | 11.48 | 307580 | 247556 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UJ | LD23UJ | ld2 3uj | ld23uj | Powys | Powys | Erwood STW | 2019 | 1029 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.18 | 10.23 | 11.31 | 311841 | 244118 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UL | LD23UL | ld2 3ul | ld23ul | Powys | Powys | Aberedw STW | 237 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 307835 | 247431 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UN | LD23UN | ld2 3un | ld23un | Powys | Powys | Aberedw STW | 353 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 307952 | 247371 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UP | LD23UP | ld2 3up | ld23up | Powys | Powys | Aberedw STW | 1516 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 308720 | 248421 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UQ | LD23UQ | ld2 3uq | ld23uq | Powys | Powys | Erwood STW | 3164 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 313066 | 244069 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UR | LD23UR | ld2 3ur | ld23ur | Powys | Powys | Aberedw STW | 1655 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 309242 | 247602 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3US | LD23US | ld2 3us | ld23us | Powys | Powys | Builth Wells STW | 1349 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 303436 | 250713 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UT | LD23UT | ld2 3ut | ld23ut | Powys | Powys | Aberedw STW | 3792 | 1105 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.6 | 10.98 | 12.14 | 311163 | 248695 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UU | LD23UU | ld2 3uu | ld23uu | Powys | Powys | Hundred House STW | 4446 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 312588 | 250194 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UW | LD23UW | ld2 3uw | ld23uw | Powys | Powys | Aberedw STW | 488 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 308082 | 247326 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UX | LD23UX | ld2 3ux | ld23ux | Powys | Powys | Erwood STW | 3847 | 1060 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.76 | 10.54 | 11.65 | 313545 | 244782 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UY | LD23UY | ld2 3uy | ld23uy | Powys | Powys | Painscastle STW | 4908 | 1078 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.09 | 10.72 | 11.84 | 313786 | 249918 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3UZ | LD23UZ | ld2 3uz | ld23uz | Powys | Powys | Erwood STW | 3030 | 1032 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.23 | 10.26 | 11.34 | 311868 | 245675 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3WY | LD23WY | ld2 3wy | ld23wy | Powys | Powys | Builth Wells STW | 839 | 1059 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.74 | 10.53 | 11.64 | 303916 | 252018 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YA | LD23YA | ld2 3ya | ld23ya | Powys | Powys | Hundred House STW | 3734 | 1059 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.74 | 10.53 | 11.64 | 312710 | 251022 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YB | LD23YB | ld2 3yb | ld23yb | Powys | Powys | Hundred House STW | 3374 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 311864 | 251089 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YD | LD23YD | ld2 3yd | ld23yd | Powys | Powys | Aberedw STW | 4498 | 1103 | 900to1200 | 2.21 | 1.62 | 1.18 | 20.56 | 10.96 | 12.12 | 311560 | 249531 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YE | LD23YE | ld2 3ye | ld23ye | Powys | Powys | Builth Road STW | 1552 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 301619 | 254551 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YF | LD23YF | ld2 3yf | ld23yf | Powys | Powys | Builth Road STW | 1377 | 1174 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.88 | 11.67 | 12.9 | 301645 | 254375 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YG | LD23YG | ld2 3yg | ld23yg | Powys | Powys | Newbridge-On-Wye STW | 5533 | 1578 | Over1500 | 3.16 | 2.31 | 1.69 | 29.41 | 15.69 | 17.34 | 296008 | 257247 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YJ | LD23YJ | ld2 3yj | ld23yj | Powys | Powys | Erwood STW | 2240 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 310147 | 245525 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YL | LD23YL | ld2 3yl | ld23yl | Powys | Powys | Builth Wells STW | 456 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 304935 | 251224 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YN | LD23YN | ld2 3yn | ld23yn | Powys | Powys | Llanfaredd STW | 665 | 1047 | 900to1200 | 2.1 | 1.53 | 1.12 | 19.51 | 10.41 | 11.5 | 306251 | 250738 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YP | LD23YP | ld2 3yp | ld23yp | Powys | Powys | Llanfaredd STW | 1509 | 1104 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.58 | 10.97 | 12.13 | 306552 | 248971 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YQ | LD23YQ | ld2 3yq | ld23yq | Powys | Powys | Erwood STW | 4158 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 312315 | 246742 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YR | LD23YR | ld2 3yr | ld23yr | Powys | Powys | Aberedw STW | 1258 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 307290 | 246181 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YS | LD23YS | ld2 3ys | ld23ys | Powys | Powys | Erwood STW | 1569 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 308578 | 243951 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YT | LD23YT | ld2 3yt | ld23yt | Powys | Powys | Erwood STW | 1131 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 308925 | 243642 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YU | LD23YU | ld2 3yu | ld23yu | Powys | Powys | Erwood STW | 997 | 1029 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.18 | 10.23 | 11.31 | 309091 | 242881 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YW | LD23YW | ld2 3yw | ld23yw | Powys | Powys | Llanfaredd STW | 1254 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 305805 | 249757 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YX | LD23YX | ld2 3yx | ld23yx | Powys | Powys | Erwood STW | 2073 | 1044 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.46 | 10.38 | 11.47 | 309063 | 245138 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 3YY | LD23YY | ld2 3yy | ld23yy | Powys | Powys | Erwood STW | 991 | 1042 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.42 | 10.36 | 11.45 | 309734 | 242336 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD2 9AP | LD29AP | ld2 9ap | ld29ap | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0AA | LD30AA | ld3 0aa | ld30aa | Powys | Powys | Talgarth STW | 912 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315381 | 233948 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AB | LD30AB | ld3 0ab | ld30ab | Powys | Powys | Talgarth STW | 1046 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315434 | 233825 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AD | LD30AD | ld3 0ad | ld30ad | Powys | Powys | Talgarth STW | 1058 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315398 | 233799 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AE | LD30AE | ld3 0ae | ld30ae | Powys | Powys | Talgarth STW | 1039 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315482 | 233851 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AG | LD30AG | ld3 0ag | ld30ag | Powys | Powys | Talgarth STW | 1046 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315528 | 233865 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AH | LD30AH | ld3 0ah | ld30ah | Powys | Powys | Talgarth STW | 975 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315455 | 233909 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AJ | LD30AJ | ld3 0aj | ld30aj | Powys | Powys | Llyswen STW | 3069 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 313230 | 241217 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0AL | LD30AL | ld3 0al | ld30al | Powys | Powys | Talgarth STW | 926 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315519 | 233995 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AN | LD30AN | ld3 0an | ld30an | Powys | Powys | Talgarth STW | 851 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315530 | 234089 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AP | LD30AP | ld3 0ap | ld30ap | Powys | Powys | Talgarth STW | 916 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315866 | 234348 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AQ | LD30AQ | ld3 0aq | ld30aq | Powys | Powys | Llyswen STW | 3303 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 312947 | 241427 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0AR | LD30AR | ld3 0ar | ld30ar | Powys | Powys | Talgarth STW | 813 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315640 | 234224 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AS | LD30AS | ld3 0as | ld30as | Powys | Powys | Talgarth STW | 908 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315666 | 234119 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AT | LD30AT | ld3 0at | ld30at | Powys | Powys | Talgarth STW | 920 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315752 | 234185 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AU | LD30AU | ld3 0au | ld30au | Powys | Powys | Talgarth STW | 1008 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315724 | 234037 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AW | LD30AW | ld3 0aw | ld30aw | Powys | Powys | Talgarth STW | 758 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315492 | 234175 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AX | LD30AX | ld3 0ax | ld30ax | Powys | Powys | Erwood STW | 3698 | 992 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.49 | 9.86 | 10.9 | 313621 | 242543 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0AY | LD30AY | ld3 0ay | ld30ay | Powys | Powys | Talgarth STW | 978 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315656 | 234021 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0AZ | LD30AZ | ld3 0az | ld30az | Powys | Powys | Llyswen STW | 2720 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 313381 | 240871 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0BA | LD30BA | ld3 0ba | ld30ba | Powys | Powys | Talgarth STW | 972 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315586 | 233981 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BB | LD30BB | ld3 0bb | ld30bb | Powys | Powys | Talgarth STW | 1148 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315644 | 233810 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BD | LD30BD | ld3 0bd | ld30bd | Powys | Powys | Talgarth STW | 1176 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315792 | 233876 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BE | LD30BE | ld3 0be | ld30be | Powys | Powys | Talgarth STW | 1267 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315770 | 233749 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BG | LD30BG | ld3 0bg | ld30bg | Powys | Powys | Talgarth STW | 1191 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315669 | 233775 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BH | LD30BH | ld3 0bh | ld30bh | Powys | Powys | Talgarth STW | 1295 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315851 | 233771 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BJ | LD30BJ | ld3 0bj | ld30bj | Powys | Powys | Llyswen STW | 1590 | 889 | 700to900 | 1.78 | 1.3 | 0.95 | 16.57 | 8.84 | 9.77 | 314447 | 239320 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0BL | LD30BL | ld3 0bl | ld30bl | Powys | Powys | Talgarth STW | 1250 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315711 | 233731 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BN | LD30BN | ld3 0bn | ld30bn | Powys | Powys | Talgarth STW | 1181 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315571 | 233735 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BP | LD30BP | ld3 0bp | ld30bp | Powys | Powys | Talgarth STW | 1169 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315476 | 233709 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BQ | LD30BQ | ld3 0bq | ld30bq | Powys | Powys | Llyswen STW | 1428 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 314724 | 238602 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0BR | LD30BR | ld3 0br | ld30br | Powys | Powys | Talgarth STW | 566 | 876 | 700to900 | 1.75 | 1.28 | 0.94 | 16.33 | 8.71 | 9.62 | 314652 | 235184 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0BS | LD30BS | ld3 0bs | ld30bs | Powys | Powys | Talgarth STW | 1286 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315536 | 233607 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BT | LD30BT | ld3 0bt | ld30bt | Powys | Powys | Talgarth STW | 1408 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315624 | 233511 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BU | LD30BU | ld3 0bu | ld30bu | Powys | Powys | Talgarth STW | 1421 | 938 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.48 | 9.32 | 10.31 | 315591 | 233483 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BW | LD30BW | ld3 0bw | ld30bw | Powys | Powys | Talgarth STW | 1107 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315482 | 233778 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BX | LD30BX | ld3 0bx | ld30bx | Powys | Powys | Llyswen STW | 1328 | 889 | 700to900 | 1.78 | 1.3 | 0.95 | 16.57 | 8.84 | 9.77 | 313661 | 239447 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0BY | LD30BY | ld3 0by | ld30by | Powys | Powys | Talgarth STW | 1543 | 938 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.48 | 9.32 | 10.31 | 315618 | 233363 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0BZ | LD30BZ | ld3 0bz | ld30bz | Powys | Powys | Llyswen STW | 2207 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 314283 | 240160 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0DA | LD30DA | ld3 0da | ld30da | Powys | Powys | Talgarth STW | 1706 | 938 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.48 | 9.32 | 10.31 | 315673 | 233210 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DB | LD30DB | ld3 0db | ld30db | Powys | Powys | Talgarth STW | 1265 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315504 | 233617 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DD | LD30DD | ld3 0dd | ld30dd | Powys | Powys | Talgarth STW | 1314 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315491 | 233561 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DE | LD30DE | ld3 0de | ld30de | Powys | Powys | Talgarth STW | 1112 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315545 | 233800 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DF | LD30DF | ld3 0df | ld30df | Powys | Powys | Talgarth STW | 1044 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315752 | 234013 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DG | LD30DG | ld3 0dg | ld30dg | Powys | Powys | Talgarth STW | 1128 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315755 | 233908 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DH | LD30DH | ld3 0dh | ld30dh | Powys | Powys | Talgarth STW | 865 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315747 | 234264 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DJ | LD30DJ | ld3 0dj | ld30dj | Powys | Powys | Llyswen STW | 1146 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 312802 | 239147 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0DL | LD30DL | ld3 0dl | ld30dl | Powys | Powys | Talgarth STW | 1477 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 316253 | 235693 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0DN | LD30DN | ld3 0dn | ld30dn | Powys | Powys | Talgarth STW | 2002 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 317034 | 235207 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DP | LD30DP | ld3 0dp | ld30dp | Powys | Powys | Velindre STW | 2286 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 317508 | 234625 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DQ | LD30DQ | ld3 0dq | ld30dq | Powys | Powys | Talgarth STW | 623 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315490 | 234344 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DR | LD30DR | ld3 0dr | ld30dr | Powys | Powys | Talgarth STW | 1533 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 315949 | 233548 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DS | LD30DS | ld3 0ds | ld30ds | Powys | Powys | Talgarth STW | 781 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314366 | 235137 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0DT | LD30DT | ld3 0dt | ld30dt | Powys | Powys | Talgarth STW | 1930 | 938 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.48 | 9.32 | 10.31 | 316003 | 233115 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DU | LD30DU | ld3 0du | ld30du | Powys | Powys | Talgarth STW | 1986 | 938 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.48 | 9.32 | 10.31 | 316038 | 233071 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DW | LD30DW | ld3 0dw | ld30dw | Powys | Powys | Talgarth STW | 1498 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 316046 | 233667 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DX | LD30DX | ld3 0dx | ld30dx | Powys | Powys | Talgarth STW | 941 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315326 | 233900 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DY | LD30DY | ld3 0dy | ld30dy | Powys | Powys | Talgarth STW | 2033 | 938 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.48 | 9.32 | 10.31 | 316365 | 233237 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0DZ | LD30DZ | ld3 0dz | ld30dz | Powys | Powys | Talgarth STW | 814 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314356 | 235191 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0EA | LD30EA | ld3 0ea | ld30ea | Powys | Powys | Talgarth STW | 2466 | 962 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.93 | 9.56 | 10.57 | 317317 | 233786 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0EB | LD30EB | ld3 0eb | ld30eb | Powys | Powys | Velindre STW | 2547 | 996 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.56 | 9.9 | 10.94 | 318425 | 234205 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0ED | LD30ED | ld3 0ed | ld30ed | Powys | Powys | Talgarth STW | 3176 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 317809 | 233195 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0EE | LD30EE | ld3 0ee | ld30ee | Powys | Powys | Talgarth STW | 4453 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 318652 | 232159 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0EF | LD30EF | ld3 0ef | ld30ef | Powys | Powys | Talgarth STW | 3058 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 316767 | 232261 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0EG | LD30EG | ld3 0eg | ld30eg | Powys | Powys | Talgarth STW | 3040 | 998 | 900to1200 | 2 | 1.46 | 1.07 | 18.6 | 9.92 | 10.96 | 316180 | 231976 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0EH | LD30EH | ld3 0eh | ld30eh | Powys | Powys | Talgarth STW | 3866 | 1004 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.71 | 9.98 | 11.03 | 316902 | 231401 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0EJ | LD30EJ | ld3 0ej | ld30ej | Powys | Powys | Talgarth STW | 3599 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 317288 | 231971 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0EL | LD30EL | ld3 0el | ld30el | Powys | Powys | Talgarth STW | 4079 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 317626 | 231626 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0EN | LD30EN | ld3 0en | ld30en | Powys | Powys | Talgarth STW | 4686 | 1004 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.71 | 9.98 | 11.03 | 316989 | 230531 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0EW | LD30EW | ld3 0ew | ld30ew | Powys | Powys | Talgarth STW | 5151 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 317237 | 230133 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0EY | LD30EY | ld3 0ey | ld30ey | Powys | Powys | Talgarth STW | 4878 | 1032 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.23 | 10.26 | 11.34 | 316223 | 230067 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0HA | LD30HA | ld3 0ha | ld30ha | Powys | Powys | Talgarth STW | 3876 | 1023 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.07 | 10.17 | 11.24 | 315573 | 230964 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0HB | LD30HB | ld3 0hb | ld30hb | Powys | Powys | Velindre STW | 292 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 318639 | 236709 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0HF | LD30HF | ld3 0hf | ld30hf | Powys | Powys | Talgarth STW | 854 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315310 | 233986 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0HG | LD30HG | ld3 0hg | ld30hg | Powys | Powys | Talgarth STW | 791 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315236 | 234032 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0HH | LD30HH | ld3 0hh | ld30hh | Powys | Powys | Talgarth STW | 545 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315219 | 234281 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0HL | LD30HL | ld3 0hl | ld30hl | Powys | Powys | Talgarth STW | 219 | 876 | 700to900 | 1.75 | 1.28 | 0.94 | 16.33 | 8.71 | 9.62 | 314890 | 234685 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0HN | LD30HN | ld3 0hn | ld30hn | Powys | Powys | Talgarth STW | 542 | 876 | 700to900 | 1.75 | 1.28 | 0.94 | 16.33 | 8.71 | 9.62 | 314536 | 234875 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0HP | LD30HP | ld3 0hp | ld30hp | Powys | Powys | Talgarth STW | 648 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314431 | 234895 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0HR | LD30HR | ld3 0hr | ld30hr | Powys | Powys | Talgarth STW | 656 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314430 | 234937 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0HS | LD30HS | ld3 0hs | ld30hs | Powys | Powys | Talgarth STW | 741 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314347 | 234951 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0HT | LD30HT | ld3 0ht | ld30ht | Powys | Powys | Talgarth STW | 798 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314294 | 234976 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0HU | LD30HU | ld3 0hu | ld30hu | Powys | Powys | Talgarth STW | 880 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314234 | 235072 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0HW | LD30HW | ld3 0hw | ld30hw | Powys | Powys | Talgarth STW | 613 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314473 | 234932 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0HX | LD30HX | ld3 0hx | ld30hx | Powys | Powys | Talgarth STW | 791 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314291 | 234924 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0HY | LD30HY | ld3 0hy | ld30hy | Powys | Powys | Talgarth STW | 1007 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314124 | 235141 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LA | LD30LA | ld3 0la | ld30la | Powys | Powys | Talgarth STW | 887 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314190 | 234884 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LB | LD30LB | ld3 0lb | ld30lb | Powys | Powys | Talgarth STW | 886 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314201 | 234961 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LD | LD30LD | ld3 0ld | ld30ld | Powys | Powys | Talgarth STW | 937 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314156 | 234995 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LE | LD30LE | ld3 0le | ld30le | Powys | Powys | Talgarth STW | 705 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314398 | 235010 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LF | LD30LF | ld3 0lf | ld30lf | Powys | Powys | Talgarth STW | 667 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314483 | 235116 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LG | LD30LG | ld3 0lg | ld30lg | Powys | Powys | Talgarth STW | 604 | 876 | 700to900 | 1.75 | 1.28 | 0.94 | 16.33 | 8.71 | 9.62 | 314537 | 235084 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LH | LD30LH | ld3 0lh | ld30lh | Powys | Powys | Talgarth STW | 618 | 876 | 700to900 | 1.75 | 1.28 | 0.94 | 16.33 | 8.71 | 9.62 | 314675 | 235279 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LJ | LD30LJ | ld3 0lj | ld30lj | Powys | Powys | Llyswen STW | 376 | 916 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.07 | 9.11 | 10.06 | 313019 | 238290 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LL | LD30LL | ld3 0ll | ld30ll | Powys | Powys | Talgarth STW | 811 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 315063 | 235617 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LN | LD30LN | ld3 0ln | ld30ln | Powys | Powys | Llyswen STW | 1871 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 314713 | 236851 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LP | LD30LP | ld3 0lp | ld30lp | Powys | Powys | Talgarth STW | 954 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314212 | 235216 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LQ | LD30LQ | ld3 0lq | ld30lq | Powys | Powys | Llyswen STW | 2999 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 313900 | 241103 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LR | LD30LR | ld3 0lr | ld30lr | Powys | Powys | Talgarth STW | 812 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314270 | 234927 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LS | LD30LS | ld3 0ls | ld30ls | Powys | Powys | Llandefalle STW | 1209 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 313491 | 235398 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LT | LD30LT | ld3 0lt | ld30lt | Powys | Powys | Talgarth STW | 1215 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 313865 | 234680 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LU | LD30LU | ld3 0lu | ld30lu | Powys | Powys | Llandefalle STW | 1253 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 313555 | 235278 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LW | LD30LW | ld3 0lw | ld30lw | Powys | Powys | Llyswen STW | 1511 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 313490 | 236646 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LX | LD30LX | ld3 0lx | ld30lx | Powys | Powys | Talgarth STW | 709 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 314452 | 235147 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0LY | LD30LY | ld3 0ly | ld30ly | Powys | Powys | Llandefalle STW | 1367 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 313674 | 235054 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NA | LD30NA | ld3 0na | ld30na | Powys | Powys | Llandefalle STW | 738 | 960 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.89 | 9.54 | 10.55 | 311760 | 235631 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NB | LD30NB | ld3 0nb | ld30nb | Powys | Powys | Llandefalle STW | 638 | 947 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.65 | 9.41 | 10.4 | 311676 | 235207 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0ND | LD30ND | ld3 0nd | ld30nd | Powys | Powys | Llandefalle STW | 1894 | 987 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.4 | 9.81 | 10.84 | 310540 | 235812 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NE | LD30NE | ld3 0ne | ld30ne | Powys | Powys | Llandefalle STW | 1008 | 960 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.89 | 9.54 | 10.55 | 311809 | 236014 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NF | LD30NF | ld3 0nf | ld30nf | Powys | Powys | Llandefalle STW | 1288 | 960 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.89 | 9.54 | 10.55 | 312406 | 236424 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NG | LD30NG | ld3 0ng | ld30ng | Powys | Powys | Llandefalle STW | 1816 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 311843 | 236894 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NH | LD30NH | ld3 0nh | ld30nh | Powys | Powys | Llyswen STW | 2294 | 998 | 900to1200 | 2 | 1.46 | 1.07 | 18.6 | 9.92 | 10.96 | 311249 | 237277 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NL | LD30NL | ld3 0nl | ld30nl | Powys | Powys | Llyswen STW | 1327 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 312070 | 237881 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NN | LD30NN | ld3 0nn | ld30nn | Powys | Powys | Llyswen STW | 1619 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 311756 | 238281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NP | LD30NP | ld3 0np | ld30np | Powys | Powys | Llyswen STW | 3024 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 310917 | 239920 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NR | LD30NR | ld3 0nr | ld30nr | Powys | Powys | Llandefalle STW | 2694 | 998 | 900to1200 | 2 | 1.46 | 1.07 | 18.6 | 9.92 | 10.96 | 310595 | 237216 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NS | LD30NS | ld3 0ns | ld30ns | Powys | Powys | Llandefalle STW | 4438 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 308831 | 237893 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NT | LD30NT | ld3 0nt | ld30nt | Powys | Powys | STW At Lower Chapel Brecon , | 5019 | 1171 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.83 | 11.64 | 12.87 | 307361 | 237686 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NU | LD30NU | ld3 0nu | ld30nu | Powys | Powys | Llandefalle STW | 4193 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 308320 | 236425 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0NW | LD30NW | ld3 0nw | ld30nw | Powys | Powys | Llyswen STW | 1992 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 311495 | 238826 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0PA | LD30PA | ld3 0pa | ld30pa | Powys | Powys | Llanfilo STW | 759 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 312414 | 234206 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0PB | LD30PB | ld3 0pb | ld30pb | Powys | Powys | Talgarth STW | 1109 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315430 | 233756 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PD | LD30PD | ld3 0pd | ld30pd | Powys | Powys | Talgarth STW | 1140 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315399 | 233714 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PE | LD30PE | ld3 0pe | ld30pe | Powys | Powys | Talgarth STW | 1081 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315367 | 233766 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PF | LD30PF | ld3 0pf | ld30pf | Powys | Powys | Talgarth STW | 1154 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315412 | 233703 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PG | LD30PG | ld3 0pg | ld30pg | Powys | Powys | Talgarth STW | 1192 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315344 | 233646 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PH | LD30PH | ld3 0ph | ld30ph | Powys | Powys | Talgarth STW | 1213 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315381 | 233633 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PL | LD30PL | ld3 0pl | ld30pl | Powys | Powys | Talgarth STW | 1309 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 315131 | 233499 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PN | LD30PN | ld3 0pn | ld30pn | Powys | Powys | Talgarth STW | 1627 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 314936 | 233185 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PP | LD30PP | ld3 0pp | ld30pp | Powys | Powys | Talgarth STW | 2798 | 927 | 900to1200 | 1.86 | 1.36 | 1 | 17.28 | 9.21 | 10.18 | 314382 | 232096 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PQ | LD30PQ | ld3 0pq | ld30pq | Powys | Powys | Talgarth STW | 1093 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 315238 | 233726 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PR | LD30PR | ld3 0pr | ld30pr | Powys | Powys | Talgarth STW | 3482 | 950 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.71 | 9.44 | 10.44 | 314524 | 231369 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PS | LD30PS | ld3 0ps | ld30ps | Powys | Powys | Llanfilo STW | 4271 | 987 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.4 | 9.81 | 10.84 | 313450 | 229996 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PT | LD30PT | ld3 0pt | ld30pt | Powys | Powys | Llanfilo STW | 4040 | 987 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.4 | 9.81 | 10.84 | 312698 | 229981 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0PU | LD30PU | ld3 0pu | ld30pu | Powys | Powys | Llanfilo STW | 2999 | 963 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.95 | 9.57 | 10.58 | 313422 | 231432 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0PW | LD30PW | ld3 0pw | ld30pw | Powys | Powys | Talgarth STW | 2827 | 927 | 900to1200 | 1.86 | 1.36 | 1 | 17.28 | 9.21 | 10.18 | 314314 | 232084 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0PY | LD30PY | ld3 0py | ld30py | Powys | Powys | Talgarth STW | 2638 | 927 | 900to1200 | 1.86 | 1.36 | 1 | 17.28 | 9.21 | 10.18 | 313925 | 232432 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RA | LD30RA | ld3 0ra | ld30ra | Powys | Powys | Talgarth STW | 1717 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 313667 | 233821 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RB | LD30RB | ld3 0rb | ld30rb | Powys | Powys | Llanfilo STW | 267 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 311987 | 233893 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RD | LD30RD | ld3 0rd | ld30rd | Powys | Powys | Llanfilo STW | 473 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 311926 | 233474 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RE | LD30RE | ld3 0re | ld30re | Powys | Powys | Llanfilo STW | 641 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 311949 | 233302 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RF | LD30RF | ld3 0rf | ld30rf | Powys | Powys | Llanfilo STW | 1381 | 995 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.55 | 9.89 | 10.93 | 310750 | 232918 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RG | LD30RG | ld3 0rg | ld30rg | Powys | Powys | Llanfilo STW | 1404 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 312623 | 232826 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RH | LD30RH | ld3 0rh | ld30rh | Powys | Powys | Llanfilo STW | 1283 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 311594 | 232624 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RL | LD30RL | ld3 0rl | ld30rl | Powys | Powys | Llanfilo STW | 2335 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 312016 | 231585 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RN | LD30RN | ld3 0rn | ld30rn | Powys | Powys | Llanfilo STW | 2229 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 310967 | 231803 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RP | LD30RP | ld3 0rp | ld30rp | Powys | Powys | Llanfilo STW | 3660 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 310131 | 230604 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RS | LD30RS | ld3 0rs | ld30rs | Powys | Powys | Velindre STW | 237 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 318574 | 236673 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0RT | LD30RT | ld3 0rt | ld30rt | Powys | Powys | Aberllynfi Three Cocks | 721 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 316977 | 237217 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RU | LD30RU | ld3 0ru | ld30ru | Powys | Powys | Talgarth STW | 1277 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 315396 | 236041 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RW | LD30RW | ld3 0rw | ld30rw | Powys | Powys | Llanfilo STW | 3129 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 309303 | 231915 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0RY | LD30RY | ld3 0ry | ld30ry | Powys | Powys | Talgarth STW | 1770 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 315781 | 236428 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SA | LD30SA | ld3 0sa | ld30sa | Powys | Powys | Aberllynfi Three Cocks | 1500 | 856 | 700to900 | 1.71 | 1.25 | 0.92 | 15.95 | 8.51 | 9.4 | 316444 | 236645 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SB | LD30SB | ld3 0sb | ld30sb | Powys | Powys | Aberllynfi Three Cocks | 1171 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 316747 | 236828 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SD | LD30SD | ld3 0sd | ld30sd | Powys | Powys | Aberllynfi Three Cocks | 766 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 316855 | 237262 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SE | LD30SE | ld3 0se | ld30se | Powys | Powys | Aberllynfi Three Cocks | 527 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 317126 | 237350 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SG | LD30SG | ld3 0sg | ld30sg | Powys | Powys | Aberllynfi Three Cocks | 311 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 317377 | 237490 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SH | LD30SH | ld3 0sh | ld30sh | Powys | Powys | Aberllynfi Three Cocks | 645 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 316759 | 237729 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SJ | LD30SJ | ld3 0sj | ld30sj | Powys | Powys | Aberllynfi Three Cocks | 77 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 317475 | 237818 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SL | LD30SL | ld3 0sl | ld30sl | Powys | Powys | Aberllynfi Three Cocks | 51 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 317350 | 237791 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SN | LD30SN | ld3 0sn | ld30sn | Powys | Powys | Aberllynfi Three Cocks | 132 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 317273 | 237834 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SP | LD30SP | ld3 0sp | ld30sp | Powys | Powys | Fforddlas STW | 1068 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 319809 | 237662 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0SQ | LD30SQ | ld3 0sq | ld30sq | Powys | Powys | Aberllynfi Three Cocks | 516 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 317037 | 237434 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SR | LD30SR | ld3 0sr | ld30sr | Powys | Powys | Velindre STW | 2253 | 1044 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.46 | 10.38 | 11.47 | 320586 | 236477 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0SS | LD30SS | ld3 0ss | ld30ss | Powys | Powys | Velindre STW | 2335 | 984 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.34 | 9.78 | 10.81 | 320339 | 235528 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0ST | LD30ST | ld3 0st | ld30st | Powys | Powys | Velindre STW | 336 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 318685 | 236780 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0SU | LD30SU | ld3 0su | ld30su | Powys | Powys | Velindre STW | 177 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 318493 | 236646 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0SW | LD30SW | ld3 0sw | ld30sw | Powys | Powys | Velindre STW | 1169 | 886 | 700to900 | 1.77 | 1.3 | 0.95 | 16.51 | 8.81 | 9.73 | 318967 | 237743 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SX | LD30SX | ld3 0sx | ld30sx | Powys | Powys | Aberllynfi Three Cocks | 1061 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 316846 | 236896 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0SY | LD30SY | ld3 0sy | ld30sy | Powys | Powys | Velindre STW | 246 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 318557 | 236618 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0SZ | LD30SZ | ld3 0sz | ld30sz | Powys | Powys | Velindre STW | 228 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 318576 | 236780 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0TA | LD30TA | ld3 0ta | ld30ta | Powys | Powys | Velindre STW | 1002 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 317487 | 236242 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0TB | LD30TB | ld3 0tb | ld30tb | Powys | Powys | Velindre STW | 610 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 318742 | 236283 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0TD | LD30TD | ld3 0td | ld30td | Powys | Powys | Velindre STW | 312 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 318640 | 236635 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0TE | LD30TE | ld3 0te | ld30te | Powys | Powys | Velindre STW | 630 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 318704 | 237271 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0TF | LD30TF | ld3 0tf | ld30tf | Powys | Powys | Aberllynfi Three Cocks | 510 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 317856 | 238027 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0TG | LD30TG | ld3 0tg | ld30tg | Powys | Powys | Velindre STW | 499 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 318686 | 236381 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 0TH | LD30TH | ld3 0th | ld30th | Powys | Powys | Llyswen STW | 994 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 312821 | 238981 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0TL | LD30TL | ld3 0tl | ld30tl | Powys | Powys | Groesffordd STW | 2959 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 309288 | 229832 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0TN | LD30TN | ld3 0tn | ld30tn | Powys | Powys | Groesffordd STW | 3334 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 309307 | 230292 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0TT | LD30TT | ld3 0tt | ld30tt | Powys | Powys | Llanfilo STW | 3682 | 1064 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.83 | 10.58 | 11.69 | 309092 | 231322 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0TU | LD30TU | ld3 0tu | ld30tu | Powys | Powys | Llanfilo STW | 3317 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 309048 | 231936 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0TY | LD30TY | ld3 0ty | ld30ty | Powys | Powys | Llanfilo STW | 3319 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 308721 | 232480 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UA | LD30UA | ld3 0ua | ld30ua | Powys | Powys | Llanfilo STW | 2461 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 309509 | 232822 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UB | LD30UB | ld3 0ub | ld30ub | Powys | Powys | Llanfilo STW | 2742 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 309066 | 233215 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UD | LD30UD | ld3 0ud | ld30ud | Powys | Powys | Llanfilo STW | 2837 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 308971 | 233202 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UE | LD30UE | ld3 0ue | ld30ue | Powys | Powys | Llanfilo STW | 2931 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 308889 | 233143 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UF | LD30UF | ld3 0uf | ld30uf | Powys | Powys | Llanfilo STW | 3700 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 308103 | 233124 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UG | LD30UG | ld3 0ug | ld30ug | Powys | Powys | Llanfilo STW | 3494 | 1051 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.59 | 10.45 | 11.55 | 308247 | 234271 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UH | LD30UH | ld3 0uh | ld30uh | Powys | Powys | Llanfilo STW | 3897 | 1052 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.61 | 10.46 | 11.56 | 307963 | 234931 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UJ | LD30UJ | ld3 0uj | ld30uj | Powys | Powys | Llanfilo STW | 2839 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 308987 | 233136 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UL | LD30UL | ld3 0ul | ld30ul | Powys | Powys | Llanfilo STW | 3555 | 1067 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.89 | 10.61 | 11.72 | 308707 | 235784 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UN | LD30UN | ld3 0un | ld30un | Powys | Powys | Llanfilo STW | 1869 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 310211 | 235001 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UP | LD30UP | ld3 0up | ld30up | Powys | Powys | Llyswen STW | 527 | 916 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.07 | 9.11 | 10.06 | 313041 | 237740 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UR | LD30UR | ld3 0ur | ld30ur | Powys | Powys | Llyswen STW | 296 | 916 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.07 | 9.11 | 10.06 | 313319 | 237860 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0US | LD30US | ld3 0us | ld30us | Powys | Powys | Llyswen STW | 360 | 916 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.07 | 9.11 | 10.06 | 313280 | 237803 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UT | LD30UT | ld3 0ut | ld30ut | Powys | Powys | Llyswen STW | 801 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 313999 | 237657 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UU | LD30UU | ld3 0uu | ld30uu | Powys | Powys | Llyswen STW | 180 | 916 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.07 | 9.11 | 10.06 | 313363 | 237972 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UW | LD30UW | ld3 0uw | ld30uw | Powys | Powys | Llanfilo STW | 1182 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 311080 | 234893 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0UY | LD30UY | ld3 0uy | ld30uy | Powys | Powys | Llyswen STW | 182 | 916 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.07 | 9.11 | 10.06 | 313207 | 238069 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YA | LD30YA | ld3 0ya | ld30ya | Powys | Powys | Llyswen STW | 295 | 916 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.07 | 9.11 | 10.06 | 313077 | 238113 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YB | LD30YB | ld3 0yb | ld30yb | Powys | Powys | Llyswen STW | 597 | 916 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.07 | 9.11 | 10.06 | 312815 | 238374 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YD | LD30YD | ld3 0yd | ld30yd | Powys | Powys | Llyswen STW | 469 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 313083 | 238523 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YE | LD30YE | ld3 0ye | ld30ye | Powys | Powys | Llyswen STW | 1483 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 312420 | 239291 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YF | LD30YF | ld3 0yf | ld30yf | Powys | Powys | Llyswen STW | 666 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 312939 | 238660 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YG | LD30YG | ld3 0yg | ld30yg | Powys | Powys | Llyswen STW | 1205 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 312812 | 239220 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YH | LD30YH | ld3 0yh | ld30yh | Powys | Powys | Llyswen STW | 980 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 313261 | 239126 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YJ | LD30YJ | ld3 0yj | ld30yj | Powys | Powys | Llyswen STW | 661 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 313011 | 238708 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YL | LD30YL | ld3 0yl | ld30yl | Powys | Powys | Llyswen STW | 500 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 313445 | 238646 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YN | LD30YN | ld3 0yn | ld30yn | Powys | Powys | Llyswen STW | 788 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 312667 | 238509 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YP | LD30YP | ld3 0yp | ld30yp | Powys | Powys | Llyswen STW | 2456 | 941 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.54 | 9.35 | 10.34 | 311851 | 240082 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YQ | LD30YQ | ld3 0yq | ld30yq | Powys | Powys | Llyswen STW | 503 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 313073 | 238558 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YR | LD30YR | ld3 0yr | ld30yr | Powys | Powys | Erwood STW | 2520 | 982 | 900to1200 | 1.97 | 1.44 | 1.05 | 18.3 | 9.76 | 10.79 | 312023 | 241789 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YS | LD30YS | ld3 0ys | ld30ys | Powys | Powys | Erwood STW | 2194 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 312085 | 242610 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YT | LD30YT | ld3 0yt | ld30yt | Powys | Powys | Erwood STW | 3056 | 956 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.82 | 9.5 | 10.5 | 312136 | 241106 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YU | LD30YU | ld3 0yu | ld30yu | Powys | Powys | Llyswen STW | 2718 | 956 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.82 | 9.5 | 10.5 | 312360 | 240675 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YW | LD30YW | ld3 0yw | ld30yw | Powys | Powys | Llyswen STW | 1535 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 312161 | 239098 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YX | LD30YX | ld3 0yx | ld30yx | Powys | Powys | Llyswen STW | 558 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 313202 | 238684 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YY | LD30YY | ld3 0yy | ld30yy | Powys | Powys | Erwood STW | 3255 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 312822 | 241670 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 0YZ | LD30YZ | ld3 0yz | ld30yz | Powys | Powys | Llyswen STW | 825 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 312874 | 238812 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7EX | LD37EX | ld3 7ex | ld37ex | Powys | Powys | Pennorth And Scethrog STW | 1362 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 311375 | 226002 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7EZ | LD37EZ | ld3 7ez | ld37ez | Powys | Powys | Pennorth And Scethrog STW | 1369 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 311229 | 226090 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7FF | LD37FF | ld3 7ff | ld37ff | Powys | Powys | Pennorth And Scethrog STW | 4137 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 313849 | 227472 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7HQ | LD37HQ | ld3 7hq | ld37hq | Powys | Powys | Talybont STW | 1797 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 313844 | 222781 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7JR | LD37JR | ld3 7jr | ld37jr | Powys | Powys | Bwlch (S) STW | 2324 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 314642 | 222459 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PJ | LD37PJ | ld3 7pj | ld37pj | Powys | Powys | Pennorth And Scethrog STW | 2121 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 312413 | 226028 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PQ | LD37PQ | ld3 7pq | ld37pq | Powys | Powys | Pennorth And Scethrog STW | 1387 | 1109 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.67 | 11.02 | 12.18 | 311192 | 226126 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PX | LD37PX | ld3 7px | ld37px | Powys | Powys | Talybont STW | 2316 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 313207 | 225072 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7PZ | LD37PZ | ld3 7pz | ld37pz | Powys | Powys | Talybont STW | 2392 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 314459 | 222993 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SX | LD37SX | ld3 7sx | ld37sx | Powys | Powys | Talybont STW | 2514 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 314553 | 223440 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SY | LD37SY | ld3 7sy | ld37sy | Powys | Powys | Pencelli STW | 2308 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 310713 | 227179 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7SZ | LD37SZ | ld3 7sz | ld37sz | Powys | Powys | Talybont STW | 3256 | 1052 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.61 | 10.46 | 11.56 | 314449 | 225276 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7TA | LD37TA | ld3 7ta | ld37ta | Powys | Powys | Pennorth And Scethrog STW | 2475 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 310882 | 227313 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7TB | LD37TB | ld3 7tb | ld37tb | Powys | Powys | Pencelli STW | 2539 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 310694 | 227474 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7TD | LD37TD | ld3 7td | ld37td | Powys | Powys | Pencelli STW | 2595 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 310760 | 227498 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7TE | LD37TE | ld3 7te | ld37te | Powys | Powys | Pennorth And Scethrog STW | 2825 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 311414 | 227569 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7TF | LD37TF | ld3 7tf | ld37tf | Powys | Powys | Pencelli STW | 3596 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 311179 | 228417 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7TG | LD37TG | ld3 7tg | ld37tg | Powys | Powys | Pennorth And Scethrog STW | 3488 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 311283 | 228279 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7TH | LD37TH | ld3 7th | ld37th | Powys | Powys | Pennorth And Scethrog STW | 3649 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 311364 | 228427 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7TJ | LD37TJ | ld3 7tj | ld37tj | Powys | Powys | Pennorth And Scethrog STW | 3495 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 311393 | 228264 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7TL | LD37TL | ld3 7tl | ld37tl | Powys | Powys | Pennorth And Scethrog STW | 3625 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 311449 | 228385 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7TN | LD37TN | ld3 7tn | ld37tn | Powys | Powys | Pennorth And Scethrog STW | 3816 | 1026 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.12 | 10.2 | 11.27 | 311652 | 228531 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7TP | LD37TP | ld3 7tp | ld37tp | Powys | Powys | Pennorth And Scethrog STW | 3575 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 311744 | 228252 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7TQ | LD37TQ | ld3 7tq | ld37tq | Powys | Powys | Talybont STW | 2787 | 1052 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.61 | 10.46 | 11.56 | 314103 | 224960 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7TR | LD37TR | ld3 7tr | ld37tr | Powys | Powys | Pennorth And Scethrog STW | 3768 | 986 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.38 | 9.8 | 10.83 | 313102 | 227710 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7TS | LD37TS | ld3 7ts | ld37ts | Powys | Powys | Pennorth And Scethrog STW | 4078 | 986 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.38 | 9.8 | 10.83 | 313486 | 227778 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7TT | LD37TT | ld3 7tt | ld37tt | Powys | Powys | Pennorth And Scethrog STW | 4237 | 986 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.38 | 9.8 | 10.83 | 313428 | 228047 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7TU | LD37TU | ld3 7tu | ld37tu | Powys | Powys | Llanfilo STW | 5197 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 314097 | 229280 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7TW | LD37TW | ld3 7tw | ld37tw | Powys | Powys | Llanfilo STW | 4363 | 1009 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.81 | 10.03 | 11.09 | 311989 | 229547 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7TX | LD37TX | ld3 7tx | ld37tx | Powys | Powys | Pencelli STW | 3527 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 311135 | 228363 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7TY | LD37TY | ld3 7ty | ld37ty | Powys | Powys | Pennorth And Scethrog STW | 3957 | 986 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.38 | 9.8 | 10.83 | 313445 | 227649 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UA | LD37UA | ld3 7ua | ld37ua | Powys | Powys | Pennorth And Scethrog STW | 3873 | 986 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.38 | 9.8 | 10.83 | 313395 | 227581 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UB | LD37UB | ld3 7ub | ld37ub | Powys | Powys | Pennorth And Scethrog STW | 3948 | 986 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.38 | 9.8 | 10.83 | 313490 | 227591 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UD | LD37UD | ld3 7ud | ld37ud | Powys | Powys | Pennorth And Scethrog STW | 4018 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 313602 | 227574 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UE | LD37UE | ld3 7ue | ld37ue | Powys | Powys | Pennorth And Scethrog STW | 4518 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 314210 | 227629 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UG | LD37UG | ld3 7ug | ld37ug | Powys | Powys | Pennorth And Scethrog STW | 4070 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 313799 | 227426 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UH | LD37UH | ld3 7uh | ld37uh | Powys | Powys | Pennorth And Scethrog STW | 4577 | 1077 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.07 | 10.71 | 11.83 | 314805 | 226767 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UL | LD37UL | ld3 7ul | ld37ul | Powys | Powys | Cwmdu STW | 5561 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 315511 | 228343 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UN | LD37UN | ld3 7un | ld37un | Powys | Powys | Talgarth STW | 5780 | 1014 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.9 | 10.08 | 11.14 | 315123 | 229028 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UP | LD37UP | ld3 7up | ld37up | Powys | Powys | Groesffordd STW | 4148 | 1012 | 900to1200 | 2.03 | 1.48 | 1.09 | 18.86 | 10.06 | 11.12 | 310987 | 229609 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 7UR | LD37UR | ld3 7ur | ld37ur | Powys | Powys | Pennorth And Scethrog STW | 4239 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 313876 | 227598 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7US | LD37US | ld3 7us | ld37us | Powys | Powys | Pennorth And Scethrog STW | 4187 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 313930 | 227451 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UU | LD37UU | ld3 7uu | ld37uu | Powys | Powys | Pennorth And Scethrog STW | 4518 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 314210 | 227629 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 7UW | LD37UW | ld3 7uw | ld37uw | Powys | Powys | Groesffordd STW | 2950 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 310135 | 228606 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 9TA | LD39TA | ld3 9ta | ld39ta | Powys | Powys | Llanddew STW | 2557 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 307585 | 231543 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 9TB | LD39TB | ld3 9tb | ld39tb | Powys | Powys | Llanddew STW | 3012 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 307862 | 232097 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 9TD | LD39TD | ld3 9td | ld39td | Powys | Powys | Llanddew STW | 1969 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 306811 | 231855 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 9TH | LD39TH | ld3 9th | ld39th | Powys | Powys | STW At Lower Chapel Brecon , | 4483 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 307184 | 235153 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD3 9TL | LD39TL | ld3 9tl | ld39tl | Powys | Powys | STW At Lower Chapel Brecon , | 2688 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 305403 | 236092 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AA | LD44AA | ld4 4aa | ld44aa | Powys | Powys | Llangammarch Wells WwTW | 321 | 1447 | 1200to1500 | 2.9 | 2.12 | 1.55 | 26.97 | 14.38 | 15.9 | 293614 | 247622 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AB | LD44AB | ld4 4ab | ld44ab | Powys | Powys | Garth STW | 473 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 295023 | 248962 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AE | LD44AE | ld4 4ae | ld44ae | Powys | Powys | Garth STW | 103 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 295132 | 249477 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AF | LD44AF | ld4 4af | ld44af | Powys | Powys | Garth STW | 149 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 295332 | 249468 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AG | LD44AG | ld4 4ag | ld44ag | Powys | Powys | Garth STW | 244 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 294999 | 249539 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AH | LD44AH | ld4 4ah | ld44ah | Powys | Powys | Garth STW | 198 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 295093 | 249566 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AJ | LD44AJ | ld4 4aj | ld44aj | Powys | Powys | Garth STW | 108 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 295307 | 249415 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AL | LD44AL | ld4 4al | ld44al | Powys | Powys | Garth STW | 975 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 294354 | 249884 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AN | LD44AN | ld4 4an | ld44an | Powys | Powys | Beulah STW | 1720 | 1422 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.5 | 14.14 | 15.62 | 293260 | 249669 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AP | LD44AP | ld4 4ap | ld44ap | Powys | Powys | Beulah STW | 1473 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 293688 | 250906 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AR | LD44AR | ld4 4ar | ld44ar | Powys | Powys | Garth STW | 272 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 295392 | 249592 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AS | LD44AS | ld4 4as | ld44as | Powys | Powys | Garth STW | 409 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 295447 | 249726 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AT | LD44AT | ld4 4at | ld44at | Powys | Powys | Garth STW | 348 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 295482 | 249604 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AU | LD44AU | ld4 4au | ld44au | Powys | Powys | Garth STW | 872 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 295841 | 249991 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AW | LD44AW | ld4 4aw | ld44aw | Powys | Powys | Garth STW | 1414 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 294126 | 250319 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4AY | LD44AY | ld4 4ay | ld44ay | Powys | Powys | Garth STW | 1651 | 1378 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.68 | 13.7 | 15.14 | 296719 | 250046 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BA | LD44BA | ld4 4ba | ld44ba | Powys | Powys | Garth STW | 2902 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 297882 | 250506 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BB | LD44BB | ld4 4bb | ld44bb | Powys | Powys | Garth STW | 2960 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 297800 | 250814 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BD | LD44BD | ld4 4bd | ld44bd | Powys | Powys | Cilmery STW | 2869 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 297933 | 251726 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BF | LD44BF | ld4 4bf | ld44bf | Powys | Powys | Llangammarch Wells WwTW | 355 | 1447 | 1200to1500 | 2.9 | 2.12 | 1.55 | 26.97 | 14.38 | 15.9 | 293715 | 247661 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BG | LD44BG | ld4 4bg | ld44bg | Powys | Powys | Garth STW | 2403 | 1285 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.95 | 12.77 | 14.12 | 296367 | 251500 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BH | LD44BH | ld4 4bh | ld44bh | Powys | Powys | Garth STW | 518 | 1384 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.8 | 13.76 | 15.21 | 295662 | 249166 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BL | LD44BL | ld4 4bl | ld44bl | Powys | Powys | Garth STW | 1546 | 1426 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.58 | 14.18 | 15.67 | 296579 | 248702 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BN | LD44BN | ld4 4bn | ld44bn | Powys | Powys | Garth STW | 1211 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 295876 | 248396 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BS | LD44BS | ld4 4bs | ld44bs | Powys | Powys | Llangammarch Wells WwTW | 803 | 1545 | Over1500 | 3.09 | 2.26 | 1.66 | 28.8 | 15.36 | 16.97 | 294473 | 247424 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BT | LD44BT | ld4 4bt | ld44bt | Powys | Powys | Llangammarch Wells WwTW | 366 | 1526 | Over1500 | 3.05 | 2.23 | 1.64 | 28.44 | 15.17 | 16.77 | 293466 | 247011 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BU | LD44BU | ld4 4bu | ld44bu | Powys | Powys | Garth STW | 1422 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 295153 | 247979 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BW | LD44BW | ld4 4bw | ld44bw | Powys | Powys | Llangammarch Wells WwTW | 259 | 1447 | 1200to1500 | 2.9 | 2.12 | 1.55 | 26.97 | 14.38 | 15.9 | 293628 | 247562 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4BY | LD44BY | ld4 4by | ld44by | Powys | Powys | Llangammarch Wells WwTW | 313 | 1526 | Over1500 | 3.05 | 2.23 | 1.64 | 28.44 | 15.17 | 16.77 | 293366 | 247320 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DA | LD44DA | ld4 4da | ld44da | Powys | Powys | Llangammarch Wells WwTW | 1898 | 1517 | Over1500 | 3.04 | 2.22 | 1.63 | 28.27 | 15.08 | 16.67 | 292204 | 248501 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DB | LD44DB | ld4 4db | ld44db | Powys | Powys | Llanwrtyd Wells STW | 2292 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 291329 | 248208 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DD | LD44DD | ld4 4dd | ld44dd | Powys | Powys | Llangammarch Wells WwTW | 1682 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 291998 | 247366 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DE | LD44DE | ld4 4de | ld44de | Powys | Powys | Llanwrtyd Wells STW | 1280 | 1487 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.72 | 14.78 | 16.34 | 291158 | 246924 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DF | LD44DF | ld4 4df | ld44df | Powys | Powys | Llanwrtyd Wells STW | 1409 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 290521 | 247640 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DG | LD44DG | ld4 4dg | ld44dg | Powys | Powys | Llangammarch Wells WwTW | 1102 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 292960 | 246473 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DH | LD44DH | ld4 4dh | ld44dh | Powys | Powys | Llanwrtyd Wells STW | 1637 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 291642 | 246604 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DJ | LD44DJ | ld4 4dj | ld44dj | Powys | Powys | Llanwrtyd Wells STW | 2236 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 290808 | 248416 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DL | LD44DL | ld4 4dl | ld44dl | Powys | Powys | Cefn Gorwydd WwTW | 646 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 290454 | 245624 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DN | LD44DN | ld4 4dn | ld44dn | Powys | Powys | Cefn Gorwydd WwTW | 511 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 290218 | 245567 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DP | LD44DP | ld4 4dp | ld44dp | Powys | Powys | Cefn Gorwydd WwTW | 1315 | 1591 | Over1500 | 3.18 | 2.33 | 1.71 | 29.65 | 15.82 | 17.48 | 289324 | 244800 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DQ | LD44DQ | ld4 4dq | ld44dq | Powys | Powys | Cefn Gorwydd WwTW | 573 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 290282 | 245539 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DR | LD44DR | ld4 4dr | ld44dr | Powys | Powys | Tirabad STW | 192 | 1601 | Over1500 | 3.2 | 2.34 | 1.72 | 29.84 | 15.91 | 17.59 | 287852 | 241300 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DS | LD44DS | ld4 4ds | ld44ds | Powys | Powys | Tirabad STW | 135 | 1601 | Over1500 | 3.2 | 2.34 | 1.72 | 29.84 | 15.91 | 17.59 | 287821 | 241388 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DU | LD44DU | ld4 4du | ld44du | Powys | Powys | Tirabad STW | 2184 | 1551 | Over1500 | 3.1 | 2.27 | 1.67 | 28.91 | 15.42 | 17.04 | 289769 | 242642 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4DW | LD44DW | ld4 4dw | ld44dw | Powys | Powys | Cefn Gorwydd WwTW | 2236 | 1584 | Over1500 | 3.17 | 2.32 | 1.7 | 29.52 | 15.75 | 17.4 | 290752 | 243904 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4EA | LD44EA | ld4 4ea | ld44ea | Powys | Powys | Llangammarch Wells WwTW | 215 | 1545 | Over1500 | 3.09 | 2.26 | 1.66 | 28.8 | 15.36 | 16.97 | 293574 | 247120 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4EB | LD44EB | ld4 4eb | ld44eb | Powys | Powys | Llangammarch Wells WwTW | 130 | 1545 | Over1500 | 3.09 | 2.26 | 1.66 | 28.8 | 15.36 | 16.97 | 293614 | 247195 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4ED | LD44ED | ld4 4ed | ld44ed | Powys | Powys | Cefn Gorwydd WwTW | 2049 | 1541 | Over1500 | 3.08 | 2.26 | 1.66 | 28.72 | 15.32 | 16.93 | 290451 | 244000 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4EE | LD44EE | ld4 4ee | ld44ee | Powys | Powys | Llangammarch Wells WwTW | 132 | 1545 | Over1500 | 3.09 | 2.26 | 1.66 | 28.8 | 15.36 | 16.97 | 293552 | 247342 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4EF | LD44EF | ld4 4ef | ld44ef | Powys | Powys | Llangammarch Wells WwTW | 163 | 1545 | Over1500 | 3.09 | 2.26 | 1.66 | 28.8 | 15.36 | 16.97 | 293576 | 247182 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4EG | LD44EG | ld4 4eg | ld44eg | Powys | Powys | Llangammarch Wells WwTW | 198 | 1545 | Over1500 | 3.09 | 2.26 | 1.66 | 28.8 | 15.36 | 16.97 | 293570 | 247143 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4EH | LD44EH | ld4 4eh | ld44eh | Powys | Powys | Llangammarch Wells WwTW | 224 | 1545 | Over1500 | 3.09 | 2.26 | 1.66 | 28.8 | 15.36 | 16.97 | 293551 | 247124 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4EL | LD44EL | ld4 4el | ld44el | Powys | Powys | Llangammarch Wells WwTW | 247 | 1545 | Over1500 | 3.09 | 2.26 | 1.66 | 28.8 | 15.36 | 16.97 | 293879 | 247164 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4EN | LD44EN | ld4 4en | ld44en | Powys | Powys | Llangammarch Wells WwTW | 637 | 1545 | Over1500 | 3.09 | 2.26 | 1.66 | 28.8 | 15.36 | 16.97 | 293716 | 246672 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4EP | LD44EP | ld4 4ep | ld44ep | Powys | Powys | Llangammarch Wells WwTW | 787 | 1526 | Over1500 | 3.05 | 2.23 | 1.64 | 28.44 | 15.17 | 16.77 | 293011 | 246892 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4ER | LD44ER | ld4 4er | ld44er | Powys | Powys | Llangammarch Wells WwTW | 1645 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 292622 | 246048 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4ES | LD44ES | ld4 4es | ld44es | Powys | Powys | Cefn Gorwydd WwTW | 1837 | 1585 | Over1500 | 3.17 | 2.32 | 1.7 | 29.54 | 15.76 | 17.41 | 291643 | 245361 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD4 4EW | LD44EW | ld4 4ew | ld44ew | Powys | Powys | Llangammarch Wells WwTW | 537 | 1526 | Over1500 | 3.05 | 2.23 | 1.64 | 28.44 | 15.17 | 16.77 | 293335 | 246896 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4AB | LD54AB | ld5 4ab | ld54ab | Powys | Powys | Beulah STW | 3703 | 1805 | Over1500 | 3.61 | 2.64 | 1.94 | 33.64 | 17.94 | 19.83 | 288735 | 249792 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4AD | LD54AD | ld5 4ad | ld54ad | Powys | Powys | Llanwrtyd Wells STW | 4199 | 1847 | Over1500 | 3.7 | 2.71 | 1.98 | 34.43 | 18.36 | 20.29 | 286074 | 247724 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4AF | LD54AF | ld5 4af | ld54af | Powys | Powys | Cefn Gorwydd WwTW | 342 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 289688 | 246234 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4AG | LD54AG | ld5 4ag | ld54ag | Powys | Powys | Llanwrtyd Wells STW | 1976 | 1761 | Over1500 | 3.52 | 2.58 | 1.89 | 32.82 | 17.51 | 19.35 | 288466 | 247527 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4AH | LD54AH | ld5 4ah | ld54ah | Powys | Powys | Cefn Gorwydd WwTW | 1886 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 288138 | 246614 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RA | LD54RA | ld5 4ra | ld54ra | Powys | Powys | Cefn Gorwydd WwTW | 2254 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 287794 | 246746 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RB | LD54RB | ld5 4rb | ld54rb | Powys | Powys | Cefn Gorwydd WwTW | 2148 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 287906 | 246742 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RD | LD54RD | ld5 4rd | ld54rd | Powys | Powys | Cefn Gorwydd WwTW | 2181 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 287887 | 246785 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RE | LD54RE | ld5 4re | ld54re | Powys | Powys | Cefn Gorwydd WwTW | 2117 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 287939 | 246741 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RF | LD54RF | ld5 4rf | ld54rf | Powys | Powys | Cefn Gorwydd WwTW | 2081 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 288005 | 246807 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RG | LD54RG | ld5 4rg | ld54rg | Powys | Powys | Cefn Gorwydd WwTW | 1978 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 288103 | 246776 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RH | LD54RH | ld5 4rh | ld54rh | Powys | Powys | Cefn Gorwydd WwTW | 2096 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 287942 | 246690 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RJ | LD54RJ | ld5 4rj | ld54rj | Powys | Powys | Cefn Gorwydd WwTW | 1788 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 288261 | 246662 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RL | LD54RL | ld5 4rl | ld54rl | Powys | Powys | Cefn Gorwydd WwTW | 1966 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 288071 | 246665 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RN | LD54RN | ld5 4rn | ld54rn | Powys | Powys | Cefn Gorwydd WwTW | 1940 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 288065 | 246567 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RP | LD54RP | ld5 4rp | ld54rp | Powys | Powys | Cefn Gorwydd WwTW | 1633 | 1631 | Over1500 | 3.26 | 2.39 | 1.75 | 30.4 | 16.21 | 17.92 | 288349 | 246448 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RQ | LD54RQ | ld5 4rq | ld54rq | Powys | Powys | Cefn Gorwydd WwTW | 1898 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 288151 | 246682 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RR | LD54RR | ld5 4rr | ld54rr | Powys | Powys | Cefn Gorwydd WwTW | 901 | 1643 | Over1500 | 3.29 | 2.41 | 1.76 | 30.62 | 16.33 | 18.05 | 289022 | 246113 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RS | LD54RS | ld5 4rs | ld54rs | Powys | Powys | Cefn Gorwydd WwTW | 1358 | 1635 | Over1500 | 3.27 | 2.39 | 1.76 | 30.47 | 16.25 | 17.96 | 288673 | 246532 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RT | LD54RT | ld5 4rt | ld54rt | Powys | Powys | Llanwrtyd Wells STW | 1878 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 288222 | 246828 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RU | LD54RU | ld5 4ru | ld54ru | Powys | Powys | Cefn Gorwydd WwTW | 1969 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 288079 | 246693 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RW | LD54RW | ld5 4rw | ld54rw | Powys | Powys | Cefn Gorwydd WwTW | 2025 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 287985 | 246598 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RX | LD54RX | ld5 4rx | ld54rx | Powys | Powys | Llanwrtyd Wells STW | 1761 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 288351 | 246849 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4RY | LD54RY | ld5 4ry | ld54ry | Powys | Powys | Cefn Gorwydd WwTW | 1853 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 288136 | 246502 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4SA | LD54SA | ld5 4sa | ld54sa | Powys | Powys | Llanwrtyd Wells STW | 1925 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 288214 | 246957 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4SB | LD54SB | ld5 4sb | ld54sb | Powys | Powys | Llanwrtyd Wells STW | 2428 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 288912 | 248475 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4SE | LD54SE | ld5 4se | ld54se | Powys | Powys | Llanwrtyd Wells STW | 1972 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 288534 | 247604 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4SF | LD54SF | ld5 4sf | ld54sf | Powys | Powys | Llanwrtyd Wells STW | 3119 | 1720 | Over1500 | 3.44 | 2.52 | 1.85 | 32.06 | 17.1 | 18.9 | 289407 | 249375 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4SG | LD54SG | ld5 4sg | ld54sg | Powys | Powys | Beulah STW | 2980 | 1805 | Over1500 | 3.61 | 2.64 | 1.94 | 33.64 | 17.94 | 19.83 | 289462 | 249916 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4SL | LD54SL | ld5 4sl | ld54sl | Powys | Powys | Llanwrtyd Wells STW | 2814 | 1761 | Over1500 | 3.52 | 2.58 | 1.89 | 32.82 | 17.51 | 19.35 | 287993 | 248261 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4SN | LD54SN | ld5 4sn | ld54sn | Powys | Powys | Llanwrtyd Wells STW | 2599 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 287522 | 246999 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4SP | LD54SP | ld5 4sp | ld54sp | Powys | Powys | Cefn Gorwydd WwTW | 2171 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 287855 | 246668 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4SR | LD54SR | ld5 4sr | ld54sr | Powys | Powys | Cefn Gorwydd WwTW | 2160 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 287854 | 246629 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4SS | LD54SS | ld5 4ss | ld54ss | Powys | Powys | Cefn Gorwydd WwTW | 2215 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 287809 | 246669 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4ST | LD54ST | ld5 4st | ld54st | Powys | Powys | Cefn Gorwydd WwTW | 2195 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 287807 | 246597 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4SU | LD54SU | ld5 4su | ld54su | Powys | Powys | Cefn Gorwydd WwTW | 2326 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 287678 | 246623 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4SY | LD54SY | ld5 4sy | ld54sy | Powys | Powys | Cefn Gorwydd WwTW | 3242 | 1753 | Over1500 | 3.51 | 2.57 | 1.88 | 32.67 | 17.43 | 19.26 | 286815 | 246933 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TA | LD54TA | ld5 4ta | ld54ta | Powys | Powys | Cefn Gorwydd WwTW | 2326 | 1631 | Over1500 | 3.26 | 2.39 | 1.75 | 30.4 | 16.21 | 17.92 | 287616 | 246346 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TB | LD54TB | ld5 4tb | ld54tb | Powys | Powys | Cefn Gorwydd WwTW | 2020 | 1631 | Over1500 | 3.26 | 2.39 | 1.75 | 30.4 | 16.21 | 17.92 | 287895 | 246083 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TD | LD54TD | ld5 4td | ld54td | Powys | Powys | Cefn Gorwydd WwTW | 1922 | 1618 | Over1500 | 3.24 | 2.37 | 1.74 | 30.16 | 16.08 | 17.78 | 288114 | 245298 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TE | LD54TE | ld5 4te | ld54te | Powys | Powys | Cefn Gorwydd WwTW | 3811 | 1717 | Over1500 | 3.44 | 2.51 | 1.84 | 32 | 17.07 | 18.86 | 286226 | 245012 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TH | LD54TH | ld5 4th | ld54th | Powys | Powys | Cefn Gorwydd WwTW | 2968 | 1753 | Over1500 | 3.51 | 2.57 | 1.88 | 32.67 | 17.43 | 19.26 | 287130 | 247007 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TL | LD54TL | ld5 4tl | ld54tl | Powys | Powys | Llanwrtyd Wells STW | 3728 | 1739 | Over1500 | 3.48 | 2.55 | 1.87 | 32.41 | 17.29 | 19.11 | 286712 | 248018 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TN | LD54TN | ld5 4tn | ld54tn | Powys | Powys | Llanwrtyd Wells STW | 5726 | 1809 | Over1500 | 3.62 | 2.65 | 1.94 | 33.72 | 17.98 | 19.88 | 285867 | 250249 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TP | LD54TP | ld5 4tp | ld54tp | Powys | Powys | Beulah STW | 6569 | 1967 | Over1500 | 3.94 | 2.88 | 2.11 | 36.66 | 19.55 | 21.61 | 285973 | 253062 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TR | LD54TR | ld5 4tr | ld54tr | Powys | Powys | Beulah STW | 9768 | 2038 | Over1500 | 4.08 | 2.98 | 2.19 | 37.99 | 20.26 | 22.39 | 283582 | 255593 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TS | LD54TS | ld5 4ts | ld54ts | Powys | Powys | Beulah STW | 5232 | 1920 | Over1500 | 3.84 | 2.81 | 2.06 | 35.79 | 19.09 | 21.09 | 288186 | 254367 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TT | LD54TT | ld5 4tt | ld54tt | Powys | Powys | Beulah STW | 2339 | 1694 | Over1500 | 3.39 | 2.48 | 1.82 | 31.57 | 16.84 | 18.61 | 290394 | 252498 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TW | LD54TW | ld5 4tw | ld54tw | Powys | Powys | Beulah STW | 7313 | 1937 | Over1500 | 3.88 | 2.84 | 2.08 | 36.1 | 19.25 | 21.28 | 284946 | 251761 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4TY | LD54TY | ld5 4ty | ld54ty | Powys | Powys | Beulah STW | 1418 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 291155 | 251974 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UA | LD54UA | ld5 4ua | ld54ua | Powys | Powys | Beulah STW | 902 | 1612 | Over1500 | 3.23 | 2.36 | 1.73 | 30.05 | 16.02 | 17.71 | 291390 | 251389 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UB | LD54UB | ld5 4ub | ld54ub | Powys | Powys | Beulah STW | 483 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 291869 | 251370 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UD | LD54UD | ld5 4ud | ld54ud | Powys | Powys | Beulah STW | 655 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 292400 | 251669 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UE | LD54UE | ld5 4ue | ld54ue | Powys | Powys | Beulah STW | 1674 | 1617 | Over1500 | 3.24 | 2.37 | 1.74 | 30.14 | 16.07 | 17.77 | 292395 | 252704 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UF | LD54UF | ld5 4uf | ld54uf | Powys | Powys | Beulah STW | 908 | 1516 | Over1500 | 3.03 | 2.22 | 1.63 | 28.26 | 15.07 | 16.66 | 292335 | 250138 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UG | LD54UG | ld5 4ug | ld54ug | Powys | Powys | Beulah STW | 2053 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 290866 | 249498 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UH | LD54UH | ld5 4uh | ld54uh | Powys | Powys | Beulah STW | 1408 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 290969 | 250396 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UL | LD54UL | ld5 4ul | ld54ul | Powys | Powys | Beulah STW | 2799 | 1814 | Over1500 | 3.63 | 2.66 | 1.95 | 33.81 | 18.03 | 19.93 | 289438 | 250751 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UN | LD54UN | ld5 4un | ld54un | Powys | Powys | Beulah STW | 2571 | 1692 | Over1500 | 3.39 | 2.48 | 1.82 | 31.54 | 16.82 | 18.59 | 289907 | 249919 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UP | LD54UP | ld5 4up | ld54up | Powys | Powys | Beulah STW | 170 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 292111 | 251169 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UR | LD54UR | ld5 4ur | ld54ur | Powys | Powys | Beulah STW | 205 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 292182 | 251240 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UT | LD54UT | ld5 4ut | ld54ut | Powys | Powys | Beulah STW | 185 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 292188 | 251221 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UU | LD54UU | ld5 4uu | ld54uu | Powys | Powys | Beulah STW | 312 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 292052 | 251301 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4UY | LD54UY | ld5 4uy | ld54uy | Powys | Powys | Beulah STW | 371 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 291960 | 251302 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4YA | LD54YA | ld5 4ya | ld54ya | Powys | Powys | Beulah STW | 484 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 291820 | 251309 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4YB | LD54YB | ld5 4yb | ld54yb | Powys | Powys | Beulah STW | 476 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 291780 | 251218 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4YD | LD54YD | ld5 4yd | ld54yd | Powys | Powys | Beulah STW | 289 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 292312 | 251313 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4YE | LD54YE | ld5 4ye | ld54ye | Powys | Powys | Beulah STW | 565 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 292335 | 251592 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4YF | LD54YF | ld5 4yf | ld54yf | Powys | Powys | Beulah STW | 1137 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 291677 | 252037 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4YG | LD54YG | ld5 4yg | ld54yg | Powys | Powys | Beulah STW | 2532 | 1619 | Over1500 | 3.24 | 2.37 | 1.74 | 30.18 | 16.09 | 17.79 | 291380 | 253427 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD5 4YH | LD54YH | ld5 4yh | ld54yh | Powys | Powys | Beulah STW | 380 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 291887 | 251219 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AB | LD65AB | ld6 5ab | ld65ab | Powys | Powys | Rhayader STW | 1041 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297037 | 267964 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AD | LD65AD | ld6 5ad | ld65ad | Powys | Powys | Rhayader STW | 1021 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297050 | 267949 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AF | LD65AF | ld6 5af | ld65af | Powys | Powys | Rhayader STW | 1030 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297022 | 267928 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AG | LD65AG | ld6 5ag | ld65ag | Powys | Powys | Rhayader STW | 1131 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296882 | 267906 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AH | LD65AH | ld6 5ah | ld65ah | Powys | Powys | Rhayader STW | 1096 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296902 | 267873 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AL | LD65AL | ld6 5al | ld65al | Powys | Powys | Rhayader STW | 1092 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296895 | 267854 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AN | LD65AN | ld6 5an | ld65an | Powys | Powys | Rhayader STW | 1095 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296869 | 267814 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AP | LD65AP | ld6 5ap | ld65ap | Powys | Powys | Rhayader STW | 1199 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296771 | 267851 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AR | LD65AR | ld6 5ar | ld65ar | Powys | Powys | Rhayader STW | 1158 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296775 | 267767 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AS | LD65AS | ld6 5as | ld65as | Powys | Powys | Rhayader STW | 1233 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296670 | 267706 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AT | LD65AT | ld6 5at | ld65at | Powys | Powys | Rhayader STW | 1146 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296916 | 267981 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AU | LD65AU | ld6 5au | ld65au | Powys | Powys | Rhayader STW | 1154 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296934 | 268017 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AW | LD65AW | ld6 5aw | ld65aw | Powys | Powys | Rhayader STW | 1243 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296749 | 267902 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5AY | LD65AY | ld6 5ay | ld65ay | Powys | Powys | Rhayader STW | 1207 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296943 | 268108 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BA | LD65BA | ld6 5ba | ld65ba | Powys | Powys | Rhayader STW | 1211 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296883 | 268045 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BB | LD65BB | ld6 5bb | ld65bb | Powys | Powys | Rhayader STW | 1260 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296959 | 268200 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BD | LD65BD | ld6 5bd | ld65bd | Powys | Powys | Rhayader STW | 1287 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296943 | 268222 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BE | LD65BE | ld6 5be | ld65be | Powys | Powys | Rhayader STW | 1302 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296951 | 268250 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BG | LD65BG | ld6 5bg | ld65bg | Powys | Powys | Rhayader STW | 1297 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296988 | 268276 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BH | LD65BH | ld6 5bh | ld65bh | Powys | Powys | Rhayader STW | 763 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297267 | 267805 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BL | LD65BL | ld6 5bl | ld65bl | Powys | Powys | Rhayader STW | 337 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 297822 | 267627 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BN | LD65BN | ld6 5bn | ld65bn | Powys | Powys | Rhayader STW | 790 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297323 | 267895 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BP | LD65BP | ld6 5bp | ld65bp | Powys | Powys | Rhayader STW | 1010 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296987 | 267846 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BT | LD65BT | ld6 5bt | ld65bt | Powys | Powys | Rhayader STW | 1094 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297046 | 268052 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BU | LD65BU | ld6 5bu | ld65bu | Powys | Powys | Rhayader STW | 1106 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297057 | 268081 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BW | LD65BW | ld6 5bw | ld65bw | Powys | Powys | Rhayader STW | 1279 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296736 | 267951 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5BY | LD65BY | ld6 5by | ld65by | Powys | Powys | Rhayader STW | 1126 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297000 | 268050 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DA | LD65DA | ld6 5da | ld65da | Powys | Powys | Rhayader STW | 1182 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297120 | 268235 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DB | LD65DB | ld6 5db | ld65db | Powys | Powys | Rhayader STW | 1152 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297386 | 268353 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DD | LD65DD | ld6 5dd | ld65dd | Powys | Powys | Rhayader STW | 1236 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297007 | 268212 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DE | LD65DE | ld6 5de | ld65de | Powys | Powys | Rhayader STW | 1277 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297033 | 268287 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DF | LD65DF | ld6 5df | ld65df | Powys | Powys | Rhayader STW | 1196 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297151 | 268274 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DG | LD65DG | ld6 5dg | ld65dg | Powys | Powys | Rhayader STW | 1253 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297136 | 268333 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DH | LD65DH | ld6 5dh | ld65dh | Powys | Powys | Rhayader STW | 1225 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297430 | 268448 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DJ | LD65DJ | ld6 5dj | ld65dj | Powys | Powys | Rhayader STW | 1276 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297085 | 268325 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DL | LD65DL | ld6 5dl | ld65dl | Powys | Powys | Rhayader STW | 1023 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297131 | 268036 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DN | LD65DN | ld6 5dn | ld65dn | Powys | Powys | Rhayader STW | 1015 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297170 | 268061 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DP | LD65DP | ld6 5dp | ld65dp | Powys | Powys | Rhayader STW | 1049 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297229 | 268149 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DR | LD65DR | ld6 5dr | ld65dr | Powys | Powys | Rhayader STW | 1006 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297362 | 268180 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DS | LD65DS | ld6 5ds | ld65ds | Powys | Powys | Rhayader STW | 992 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297222 | 268073 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DY | LD65DY | ld6 5dy | ld65dy | Powys | Powys | Rhayader STW | 1022 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 297626 | 268291 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5DZ | LD65DZ | ld6 5dz | ld65dz | Powys | Powys | Rhayader STW | 1122 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 297800 | 268411 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5EA | LD65EA | ld6 5ea | ld65ea | Powys | Powys | Rhayader STW | 983 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297302 | 268119 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5EB | LD65EB | ld6 5eb | ld65eb | Powys | Powys | Rhayader STW | 955 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297249 | 268047 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5ED | LD65ED | ld6 5ed | ld65ed | Powys | Powys | Rhayader STW | 957 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297262 | 268060 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5EE | LD65EE | ld6 5ee | ld65ee | Powys | Powys | Rhayader STW | 933 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297225 | 268000 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5EF | LD65EF | ld6 5ef | ld65ef | Powys | Powys | Rhayader STW | 1073 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 297546 | 268324 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5EG | LD65EG | ld6 5eg | ld65eg | Powys | Powys | Rhayader STW | 1123 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 297550 | 268377 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5EH | LD65EH | ld6 5eh | ld65eh | Powys | Powys | Rhayader STW | 1068 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297411 | 268272 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5EL | LD65EL | ld6 5el | ld65el | Powys | Powys | Rhayader STW | 1102 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297281 | 268245 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5EN | LD65EN | ld6 5en | ld65en | Powys | Powys | Rhayader STW | 848 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 297714 | 268130 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5EP | LD65EP | ld6 5ep | ld65ep | Powys | Powys | Rhayader STW | 1246 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 297508 | 268493 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5ER | LD65ER | ld6 5er | ld65er | Powys | Powys | Rhayader STW | 962 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297479 | 268185 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5ES | LD65ES | ld6 5es | ld65es | Powys | Powys | Rhayader STW | 1062 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297291 | 268205 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5EU | LD65EU | ld6 5eu | ld65eu | Powys | Powys | Rhayader STW | 1457 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 296493 | 267869 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5EW | LD65EW | ld6 5ew | ld65ew | Powys | Powys | Rhayader STW | 941 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 297647 | 268213 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5EY | LD65EY | ld6 5ey | ld65ey | Powys | Powys | Rhayader STW | 2551 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 295508 | 268344 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HA | LD65HA | ld6 5ha | ld65ha | Powys | Powys | Rhayader STW | 3796 | 1448 | 1200to1500 | 2.9 | 2.12 | 1.56 | 26.99 | 14.39 | 15.91 | 295144 | 269971 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HB | LD65HB | ld6 5hb | ld65hb | Powys | Powys | Elan Village STW | 2504 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 294900 | 267481 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HD | LD65HD | ld6 5hd | ld65hd | Powys | Powys | Elan Village STW | 1789 | 1413 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.34 | 14.05 | 15.52 | 294410 | 266939 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HE | LD65HE | ld6 5he | ld65he | Powys | Powys | Elan Glan-Yr-Afon STW | 3276 | 1652 | Over1500 | 3.31 | 2.42 | 1.77 | 30.79 | 16.42 | 18.15 | 290358 | 264383 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HF | LD65HF | ld6 5hf | ld65hf | Powys | Powys | Elan Glan-Yr-Afon STW | 5758 | 1798 | Over1500 | 3.6 | 2.63 | 1.93 | 33.51 | 17.87 | 19.75 | 288248 | 262974 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HG | LD65HG | ld6 5hg | ld65hg | Powys | Powys | Rhayader STW | 1087 | 1301 | 1200to1500 | 2.6 | 1.91 | 1.4 | 24.25 | 12.93 | 14.29 | 296745 | 267348 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HH | LD65HH | ld6 5hh | ld65hh | Powys | Powys | Rhayader STW | 1864 | 1365 | 1200to1500 | 2.73 | 2 | 1.47 | 25.44 | 13.57 | 15 | 295967 | 267238 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HL | LD65HL | ld6 5hl | ld65hl | Powys | Powys | Elan Village STW | 1549 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 294584 | 266530 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HN | LD65HN | ld6 5hn | ld65hn | Powys | Powys | Elan Village STW | 498 | 1490 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.77 | 14.81 | 16.37 | 293789 | 265807 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HP | LD65HP | ld6 5hp | ld65hp | Powys | Powys | Elan Glan-Yr-Afon STW | 519 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 293271 | 264907 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HR | LD65HR | ld6 5hr | ld65hr | Powys | Powys | Elan Glan-Yr-Afon STW | 1019 | 1541 | Over1500 | 3.08 | 2.26 | 1.66 | 28.72 | 15.32 | 16.93 | 293189 | 264407 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HS | LD65HS | ld6 5hs | ld65hs | Powys | Powys | Elan Glan-Yr-Afon STW | 6517 | 1796 | Over1500 | 3.59 | 2.63 | 1.93 | 33.47 | 17.85 | 19.73 | 288850 | 269972 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HT | LD65HT | ld6 5ht | ld65ht | Powys | Powys | Rhayader STW | 3364 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 294977 | 269071 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HW | LD65HW | ld6 5hw | ld65hw | Powys | Powys | Elan Glan-Yr-Afon STW | 40 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 293437 | 265377 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5HY | LD65HY | ld6 5hy | ld65hy | Powys | Powys | Elan Village STW | 148 | 1490 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.77 | 14.81 | 16.37 | 293587 | 265507 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LA | LD65LA | ld6 5la | ld65la | Powys | Powys | Rhayader STW | 1437 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296898 | 268383 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LB | LD65LB | ld6 5lb | ld65lb | Powys | Powys | Rhayader STW | 1673 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 296786 | 268597 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LD | LD65LD | ld6 5ld | ld65ld | Powys | Powys | Rhayader STW | 3582 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 295540 | 270043 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LE | LD65LE | ld6 5le | ld65le | Powys | Powys | Pantydwr STW | 4483 | 1509 | Over1500 | 3.02 | 2.21 | 1.62 | 28.13 | 15 | 16.58 | 294491 | 272407 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LF | LD65LF | ld6 5lf | ld65lf | Powys | Powys | Pantydwr STW | 3072 | 1474 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.47 | 14.65 | 16.19 | 296353 | 272310 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LG | LD65LG | ld6 5lg | ld65lg | Powys | Powys | Pantydwr STW | 1714 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 298370 | 272887 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LH | LD65LH | ld6 5lh | ld65lh | Powys | Powys | Pantydwr STW | 1615 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 298669 | 273008 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LJ | LD65LJ | ld6 5lj | ld65lj | Powys | Powys | Pantydwr STW | 888 | 1362 | 1200to1500 | 2.73 | 1.99 | 1.46 | 25.39 | 13.54 | 14.96 | 298498 | 273718 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LL | LD65LL | ld6 5ll | ld65ll | Powys | Powys | Pantydwr STW | 28 | 1317 | 1200to1500 | 2.64 | 1.93 | 1.41 | 24.55 | 13.09 | 14.47 | 298378 | 274582 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LN | LD65LN | ld6 5ln | ld65ln | Powys | Powys | Pantydwr STW | 274 | 1317 | 1200to1500 | 2.64 | 1.93 | 1.41 | 24.55 | 13.09 | 14.47 | 298392 | 274874 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LQ | LD65LQ | ld6 5lq | ld65lq | Powys | Powys | Pantydwr STW | 2222 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 299078 | 272485 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LR | LD65LR | ld6 5lr | ld65lr | Powys | Powys | Pantydwr STW | 2359 | 1536 | Over1500 | 3.07 | 2.25 | 1.65 | 28.63 | 15.27 | 16.88 | 296376 | 275810 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LS | LD65LS | ld6 5ls | ld65ls | Powys | Powys | Rhayader STW | 1273 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297225 | 268410 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LT | LD65LT | ld6 5lt | ld65lt | Powys | Powys | Rhayader STW | 2385 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 297333 | 269622 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LU | LD65LU | ld6 5lu | ld65lu | Powys | Powys | Pantydwr STW | 2161 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 298989 | 272521 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LX | LD65LX | ld6 5lx | ld65lx | Powys | Powys | Pantydwr STW | 2086 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 299000 | 272603 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LY | LD65LY | ld6 5ly | ld65ly | Powys | Powys | Pantydwr STW | 1133 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 299525 | 274470 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5LZ | LD65LZ | ld6 5lz | ld65lz | Powys | Powys | Pantydwr STW | 1798 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 298693 | 272827 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NA | LD65NA | ld6 5na | ld65na | Powys | Powys | Pantydwr STW | 1117 | 1228 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.89 | 12.21 | 13.49 | 299293 | 275270 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NB | LD65NB | ld6 5nb | ld65nb | Powys | Powys | Pantydwr STW | 3741 | 1279 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.84 | 12.71 | 14.05 | 301483 | 276718 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5ND | LD65ND | ld6 5nd | ld65nd | Powys | Powys | Pantydwr STW | 4235 | 1213 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.61 | 12.06 | 13.33 | 302628 | 274818 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NE | LD65NE | ld6 5ne | ld65ne | Powys | Powys | Abbeycwmhir WwTW | 4279 | 1213 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.61 | 12.06 | 13.33 | 303147 | 274545 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NF | LD65NF | ld6 5nf | ld65nf | Powys | Powys | Pantydwr STW | 5158 | 1191 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.2 | 11.84 | 13.09 | 303323 | 276134 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NG | LD65NG | ld6 5ng | ld65ng | Powys | Powys | Pantydwr STW | 2588 | 1224 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.81 | 12.17 | 13.45 | 300226 | 272767 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NH | LD65NH | ld6 5nh | ld65nh | Powys | Powys | Rhayader STW | 4150 | 1275 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.76 | 12.67 | 14.01 | 300851 | 270133 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NL | LD65NL | ld6 5nl | ld65nl | Powys | Powys | Rhayader STW | 3794 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 300988 | 269390 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NN | LD65NN | ld6 5nn | ld65nn | Powys | Powys | Rhayader STW | 1195 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297224 | 268320 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NP | LD65NP | ld6 5np | ld65np | Powys | Powys | Rhayader STW | 1391 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 297335 | 268590 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NR | LD65NR | ld6 5nr | ld65nr | Powys | Powys | Rhayader STW | 1718 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 297516 | 268979 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NS | LD65NS | ld6 5ns | ld65ns | Powys | Powys | Rhayader STW | 2635 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 298794 | 269742 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NT | LD65NT | ld6 5nt | ld65nt | Powys | Powys | Rhayader STW | 2716 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 299704 | 269255 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NU | LD65NU | ld6 5nu | ld65nu | Powys | Powys | Rhayader STW | 961 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 298189 | 268181 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5NY | LD65NY | ld6 5ny | ld65ny | Powys | Powys | Rhayader STW | 1727 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 299325 | 268154 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5PA | LD65PA | ld6 5pa | ld65pa | Powys | Powys | Rhayader STW | 1577 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 298896 | 268451 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5PB | LD65PB | ld6 5pb | ld65pb | Powys | Powys | Rhayader STW | 2323 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 300069 | 267907 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5PD | LD65PD | ld6 5pd | ld65pd | Powys | Powys | Rhayader STW | 2366 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 300182 | 267042 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5PE | LD65PE | ld6 5pe | ld65pe | Powys | Powys | Abbeycwmhir WwTW | 4297 | 1130 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.06 | 11.23 | 12.42 | 302538 | 267912 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5PL | LD65PL | ld6 5pl | ld65pl | Powys | Powys | Rhayader STW | 1402 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 296976 | 268402 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5PN | LD65PN | ld6 5pn | ld65pn | Powys | Powys | Rhayader STW | 1333 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 297314 | 268519 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5PP | LD65PP | ld6 5pp | ld65pp | Powys | Powys | Rhayader STW | 1405 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297071 | 268472 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5PW | LD65PW | ld6 5pw | ld65pw | Powys | Powys | Rhayader STW | 1429 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 297112 | 268525 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD6 5WL | LD65WL | ld6 5wl | ld65wl | Powys | Powys | Rhayader STW | 989 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 297234 | 268079 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1LY | LD71LY | ld7 1ly | ld71ly | Powys | Powys | Presteigne STW | 5931 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 332322 | 270293 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1NH | LD71NH | ld7 1nh | ld71nh | Powys | Powys | Presteigne STW | 6600 | 1025 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.1 | 10.19 | 11.26 | 328064 | 269480 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1NJ | LD71NJ | ld7 1nj | ld71nj | Powys | Powys | Evenjobb STW | 5035 | 1004 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.71 | 9.98 | 11.03 | 327273 | 267219 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1NL | LD71NL | ld7 1nl | ld71nl | Powys | Powys | Evenjobb STW | 6122 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 327497 | 268283 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1NN | LD71NN | ld7 1nn | ld71nn | Powys | Powys | Evenjobb STW | 5011 | 1004 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.71 | 9.98 | 11.03 | 327202 | 267208 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1NP | LD71NP | ld7 1np | ld71np | Powys | Powys | Evenjobb STW | 5498 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 326522 | 267764 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1NQ | LD71NQ | ld7 1nq | ld71nq | Powys | Powys | Evenjobb STW | 4967 | 1004 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.71 | 9.98 | 11.03 | 327165 | 267169 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1NR | LD71NR | ld7 1nr | ld71nr | Powys | Powys | Llangunllo STW | 4260 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 324685 | 268060 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1NS | LD71NS | ld7 1ns | ld71ns | Powys | Powys | Llangunllo STW | 3262 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 323811 | 268580 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1NT | LD71NT | ld7 1nt | ld71nt | Powys | Powys | Llangunllo STW | 3043 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 323558 | 268637 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1NU | LD71NU | ld7 1nu | ld71nu | Powys | Powys | Llangunllo STW | 3530 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 323600 | 268032 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1NW | LD71NW | ld7 1nw | ld71nw | Powys | Powys | Evenjobb STW | 4728 | 1004 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.71 | 9.98 | 11.03 | 326805 | 266975 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1NY | LD71NY | ld7 1ny | ld71ny | Powys | Powys | Llangunllo STW | 2965 | 1170 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.81 | 11.63 | 12.85 | 322165 | 267953 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1PA | LD71PA | ld7 1pa | ld71pa | Powys | Powys | Llangunllo STW | 2757 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 320402 | 268281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1PB | LD71PB | ld7 1pb | ld71pb | Powys | Powys | Llangunllo STW | 4176 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 319569 | 267103 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1PD | LD71PD | ld7 1pd | ld71pd | Powys | Powys | Llangunllo STW | 6212 | 1009 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.81 | 10.03 | 11.09 | 327452 | 269237 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1SF | LD71SF | ld7 1sf | ld71sf | Powys | Powys | Llangunllo STW | 3511 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 324938 | 270436 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1SG | LD71SG | ld7 1sg | ld71sg | Powys | Powys | Llangunllo STW | 2673 | 1139 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.23 | 11.32 | 12.51 | 323946 | 269876 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1SH | LD71SH | ld7 1sh | ld71sh | Powys | Powys | Llangunllo STW | 2461 | 1117 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.82 | 11.1 | 12.27 | 323462 | 269414 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1SL | LD71SL | ld7 1sl | ld71sl | Powys | Powys | Llangunllo STW | 1031 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 322361 | 270348 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1SN | LD71SN | ld7 1sn | ld71sn | Powys | Powys | Llangunllo STW | 311 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 321484 | 271139 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1SP | LD71SP | ld7 1sp | ld71sp | Powys | Powys | Llangunllo STW | 693 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 321048 | 271394 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1SR | LD71SR | ld7 1sr | ld71sr | Powys | Powys | Llangunllo STW | 826 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 320696 | 271166 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1SS | LD71SS | ld7 1ss | ld71ss | Powys | Powys | Llangunllo STW | 692 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 321235 | 271487 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1ST | LD71ST | ld7 1st | ld71st | Powys | Powys | Llangunllo STW | 1222 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 321041 | 271981 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1SU | LD71SU | ld7 1su | ld71su | Powys | Powys | Llangunllo STW | 2320 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 319521 | 272117 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1SW | LD71SW | ld7 1sw | ld71sw | Powys | Powys | Llangunllo STW | 553 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 321201 | 271324 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1SY | LD71SY | ld7 1sy | ld71sy | Powys | Powys | Llangunllo STW | 2900 | 1180 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.99 | 11.73 | 12.96 | 320781 | 273651 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1TA | LD71TA | ld7 1ta | ld71ta | Powys | Powys | Llangunllo STW | 1690 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 321513 | 272518 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1TB | LD71TB | ld7 1tb | ld71tb | Powys | Powys | Llangunllo STW | 2380 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 322873 | 272737 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 1TD | LD71TD | ld7 1td | ld71td | Powys | Powys | Llangunllo STW | 1588 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 322788 | 271685 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD7 9AP | LD79AP | ld7 9ap | ld79ap | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AA | LD82AA | ld8 2aa | ld82aa | Powys | Powys | Presteigne STW | 797 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331437 | 264424 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AB | LD82AB | ld8 2ab | ld82ab | Powys | Powys | Presteigne STW | 728 | 895 | 700to900 | 1.79 | 1.31 | 0.96 | 16.68 | 8.9 | 9.83 | 331520 | 264514 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AD | LD82AD | ld8 2ad | ld82ad | Powys | Powys | Presteigne STW | 758 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331476 | 264421 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AE | LD82AE | ld8 2ae | ld82ae | Powys | Powys | Presteigne STW | 696 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331544 | 264469 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AF | LD82AF | ld8 2af | ld82af | Powys | Powys | Presteigne STW | 655 | 895 | 700to900 | 1.79 | 1.31 | 0.96 | 16.68 | 8.9 | 9.83 | 331593 | 264508 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AG | LD82AG | ld8 2ag | ld82ag | Powys | Powys | Presteigne STW | 595 | 895 | 700to900 | 1.79 | 1.31 | 0.96 | 16.68 | 8.9 | 9.83 | 331669 | 264557 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AH | LD82AH | ld8 2ah | ld82ah | Powys | Powys | Presteigne STW | 689 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331545 | 264408 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AJ | LD82AJ | ld8 2aj | ld82aj | Powys | Powys | Presteigne STW | 650 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331981 | 263766 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AN | LD82AN | ld8 2an | ld82an | Powys | Powys | Presteigne STW | 701 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331532 | 264397 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AP | LD82AP | ld8 2ap | ld82ap | Powys | Powys | Presteigne STW | 734 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331499 | 264326 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AQ | LD82AQ | ld8 2aq | ld82aq | Powys | Powys | Presteigne STW | 619 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331628 | 264499 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AR | LD82AR | ld8 2ar | ld82ar | Powys | Powys | Presteigne STW | 658 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331583 | 264259 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AS | LD82AS | ld8 2as | ld82as | Powys | Powys | Presteigne STW | 606 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331647 | 264207 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AT | LD82AT | ld8 2at | ld82at | Powys | Powys | Presteigne STW | 704 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331536 | 264264 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AU | LD82AU | ld8 2au | ld82au | Powys | Powys | Presteigne STW | 772 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331462 | 264311 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AW | LD82AW | ld8 2aw | ld82aw | Powys | Powys | Presteigne STW | 770 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331463 | 264342 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AX | LD82AX | ld8 2ax | ld82ax | Powys | Powys | Presteigne STW | 1488 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 330826 | 264850 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AY | LD82AY | ld8 2ay | ld82ay | Powys | Powys | Presteigne STW | 512 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331843 | 264032 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2AZ | LD82AZ | ld8 2az | ld82az | Powys | Powys | New Radnor STW | 365 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 321603 | 260452 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BA | LD82BA | ld8 2ba | ld82ba | Powys | Powys | Presteigne STW | 861 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331377 | 264462 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BB | LD82BB | ld8 2bb | ld82bb | Powys | Powys | Presteigne STW | 983 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331277 | 264596 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BD | LD82BD | ld8 2bd | ld82bd | Powys | Powys | Presteigne STW | 840 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331392 | 264379 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BE | LD82BE | ld8 2be | ld82be | Powys | Powys | Presteigne STW | 875 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331361 | 264449 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BG | LD82BG | ld8 2bg | ld82bg | Powys | Powys | Presteigne STW | 1092 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331181 | 264660 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BH | LD82BH | ld8 2bh | ld82bh | Powys | Powys | Presteigne STW | 1056 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331208 | 264621 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BL | LD82BL | ld8 2bl | ld82bl | Powys | Powys | Presteigne STW | 1141 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331130 | 264659 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BP | LD82BP | ld8 2bp | ld82bp | Powys | Powys | Presteigne STW | 876 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331380 | 264567 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BS | LD82BS | ld8 2bs | ld82bs | Powys | Powys | Presteigne STW | 760 | 895 | 700to900 | 1.79 | 1.31 | 0.96 | 16.68 | 8.9 | 9.83 | 331505 | 264587 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BT | LD82BT | ld8 2bt | ld82bt | Powys | Powys | Presteigne STW | 774 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331491 | 264588 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BU | LD82BU | ld8 2bu | ld82bu | Powys | Powys | Presteigne STW | 773 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331497 | 264602 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BW | LD82BW | ld8 2bw | ld82bw | Powys | Powys | Presteigne STW | 1299 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 330985 | 264729 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2BY | LD82BY | ld8 2by | ld82by | Powys | Powys | Presteigne STW | 889 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331392 | 264654 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DA | LD82DA | ld8 2da | ld82da | Powys | Powys | Presteigne STW | 1002 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331282 | 264684 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DB | LD82DB | ld8 2db | ld82db | Powys | Powys | Presteigne STW | 960 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331313 | 264640 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DD | LD82DD | ld8 2dd | ld82dd | Powys | Powys | Presteigne STW | 1023 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331228 | 264559 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DE | LD82DE | ld8 2de | ld82de | Powys | Powys | Presteigne STW | 661 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331625 | 264103 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DG | LD82DG | ld8 2dg | ld82dg | Powys | Powys | Presteigne STW | 440 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331818 | 264216 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DH | LD82DH | ld8 2dh | ld82dh | Powys | Powys | Presteigne STW | 1446 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 330821 | 264678 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DL | LD82DL | ld8 2dl | ld82dl | Powys | Powys | Presteigne STW | 781 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331466 | 264214 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DN | LD82DN | ld8 2dn | ld82dn | Powys | Powys | Presteigne STW | 732 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331523 | 264183 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DP | LD82DP | ld8 2dp | ld82dp | Powys | Powys | Presteigne STW | 935 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331299 | 264428 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DR | LD82DR | ld8 2dr | ld82dr | Powys | Powys | Presteigne STW | 825 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331407 | 264366 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DS | LD82DS | ld8 2ds | ld82ds | Powys | Powys | Presteigne STW | 907 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331328 | 264290 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DT | LD82DT | ld8 2dt | ld82dt | Powys | Powys | Presteigne STW | 885 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331347 | 264352 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DU | LD82DU | ld8 2du | ld82du | Powys | Powys | Presteigne STW | 875 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331378 | 264174 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DW | LD82DW | ld8 2dw | ld82dw | Powys | Powys | Presteigne STW | 689 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331588 | 264122 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DX | LD82DX | ld8 2dx | ld82dx | Powys | Powys | Presteigne STW | 3538 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 330118 | 267200 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2DY | LD82DY | ld8 2dy | ld82dy | Powys | Powys | Presteigne STW | 1012 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331222 | 264427 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EA | LD82EA | ld8 2ea | ld82ea | Powys | Powys | Presteigne STW | 1067 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331166 | 264393 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EB | LD82EB | ld8 2eb | ld82eb | Powys | Powys | Presteigne STW | 1063 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331171 | 264424 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2ED | LD82ED | ld8 2ed | ld82ed | Powys | Powys | Presteigne STW | 3756 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 328743 | 265752 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EE | LD82EE | ld8 2ee | ld82ee | Powys | Powys | Evenjobb STW | 3866 | 972 | 900to1200 | 1.95 | 1.42 | 1.04 | 18.12 | 9.66 | 10.68 | 328377 | 265565 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EF | LD82EF | ld8 2ef | ld82ef | Powys | Powys | Presteigne STW | 3071 | 947 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.65 | 9.41 | 10.4 | 329828 | 266275 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EG | LD82EG | ld8 2eg | ld82eg | Powys | Powys | Presteigne STW | 3607 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 329424 | 266627 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EH | LD82EH | ld8 2eh | ld82eh | Powys | Powys | Presteigne STW | 3077 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 330421 | 266851 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EL | LD82EL | ld8 2el | ld82el | Powys | Powys | Presteigne STW | 3207 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 330425 | 267013 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EN | LD82EN | ld8 2en | ld82en | Powys | Powys | Presteigne STW | 3470 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 330264 | 267221 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EP | LD82EP | ld8 2ep | ld82ep | Powys | Powys | Presteigne STW | 4896 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 329197 | 268205 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EQ | LD82EQ | ld8 2eq | ld82eq | Powys | Powys | Presteigne STW | 3185 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 330350 | 266933 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2ER | LD82ER | ld8 2er | ld82er | Powys | Powys | Presteigne STW | 5115 | 995 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.55 | 9.89 | 10.93 | 329730 | 268824 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2ES | LD82ES | ld8 2es | ld82es | Powys | Powys | Presteigne STW | 1197 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331127 | 264823 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2ET | LD82ET | ld8 2et | ld82et | Powys | Powys | Presteigne STW | 1595 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 330876 | 265203 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EU | LD82EU | ld8 2eu | ld82eu | Powys | Powys | Presteigne STW | 2064 | 937 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.46 | 9.31 | 10.29 | 330972 | 265999 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EW | LD82EW | ld8 2ew | ld82ew | Powys | Powys | Presteigne STW | 4099 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 330156 | 267898 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2EY | LD82EY | ld8 2ey | ld82ey | Powys | Powys | Presteigne STW | 3406 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 330480 | 267284 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2HA | LD82HA | ld8 2ha | ld82ha | Powys | Powys | Presteigne STW | 4559 | 989 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.43 | 9.83 | 10.87 | 330852 | 268709 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2HB | LD82HB | ld8 2hb | ld82hb | Powys | Powys | Presteigne STW | 3430 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 331368 | 267683 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2HD | LD82HD | ld8 2hd | ld82hd | Powys | Powys | Presteigne STW | 2106 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 331501 | 266339 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2HE | LD82HE | ld8 2he | ld82he | Powys | Powys | Presteigne STW | 789 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 331460 | 264528 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2HF | LD82HF | ld8 2hf | ld82hf | Powys | Powys | Presteigne STW | 518 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331772 | 264128 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2HG | LD82HG | ld8 2hg | ld82hg | Powys | Powys | Presteigne STW | 832 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 332755 | 263718 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2HX | LD82HX | ld8 2hx | ld82hx | Powys | Powys | Presteigne STW | 534 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 332158 | 263836 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2LA | LD82LA | ld8 2la | ld82la | Powys | Powys | Presteigne STW | 795 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331643 | 263831 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2LB | LD82LB | ld8 2lb | ld82lb | Powys | Powys | Presteigne STW | 361 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 332042 | 264058 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2LD | LD82LD | ld8 2ld | ld82ld | Powys | Powys | Presteigne STW | 846 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 332098 | 263530 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2LF | LD82LF | ld8 2lf | ld82lf | Powys | Powys | Presteigne STW | 529 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 332047 | 263870 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NE | LD82NE | ld8 2ne | ld82ne | Powys | Powys | Presteigne STW | 1131 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331135 | 264091 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NF | LD82NF | ld8 2nf | ld82nf | Powys | Powys | Presteigne STW | 2768 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 329697 | 265473 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NG | LD82NG | ld8 2ng | ld82ng | Powys | Powys | Evenjobb STW | 1057 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 327101 | 263020 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NH | LD82NH | ld8 2nh | ld82nh | Powys | Powys | Presteigne STW | 1837 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 330470 | 263849 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NJ | LD82NJ | ld8 2nj | ld82nj | Powys | Powys | Presteigne STW | 1085 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331158 | 264211 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NL | LD82NL | ld8 2nl | ld82nl | Powys | Powys | Presteigne STW | 2667 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 329578 | 264622 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NN | LD82NN | ld8 2nn | ld82nn | Powys | Powys | Evenjobb STW | 2175 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 327687 | 263990 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NP | LD82NP | ld8 2np | ld82np | Powys | Powys | Presteigne STW | 3446 | 936 | 900to1200 | 1.87 | 1.37 | 1.01 | 17.45 | 9.3 | 10.28 | 328856 | 265048 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NQ | LD82NQ | ld8 2nq | ld82nq | Powys | Powys | Presteigne STW | 2791 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 329622 | 265350 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NR | LD82NR | ld8 2nr | ld82nr | Powys | Powys | Evenjobb STW | 2946 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327115 | 265116 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NS | LD82NS | ld8 2ns | ld82ns | Powys | Powys | Evenjobb STW | 3259 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 326829 | 265494 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NT | LD82NT | ld8 2nt | ld82nt | Powys | Powys | Evenjobb STW | 4576 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 323973 | 266174 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NU | LD82NU | ld8 2nu | ld82nu | Powys | Powys | Old Radnor STW | 1585 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 325649 | 260622 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NW | LD82NW | ld8 2nw | ld82nw | Powys | Powys | Evenjobb STW | 2821 | 944 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.59 | 9.38 | 10.37 | 327646 | 264778 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NX | LD82NX | ld8 2nx | ld82nx | Powys | Powys | Presteigne STW | 3582 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 330206 | 267318 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2NY | LD82NY | ld8 2ny | ld82ny | Powys | Powys | Presteigne STW | 1307 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 330963 | 264053 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PA | LD82PA | ld8 2pa | ld82pa | Powys | Powys | Evenjobb STW | 887 | 1002 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.68 | 9.96 | 11.01 | 326203 | 263143 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PB | LD82PB | ld8 2pb | ld82pb | Powys | Powys | Evenjobb STW | 1916 | 1012 | 900to1200 | 2.03 | 1.48 | 1.09 | 18.86 | 10.06 | 11.12 | 326525 | 264178 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PD | LD82PD | ld8 2pd | ld82pd | Powys | Powys | Evenjobb STW | 2010 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 324905 | 263659 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PE | LD82PE | ld8 2pe | ld82pe | Powys | Powys | Evenjobb STW | 2035 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 324448 | 262974 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PF | LD82PF | ld8 2pf | ld82pf | Powys | Powys | Evenjobb STW | 3063 | 1113 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.74 | 11.06 | 12.23 | 323858 | 264040 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PG | LD82PG | ld8 2pg | ld82pg | Powys | Powys | Evenjobb STW | 2644 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 323865 | 263151 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PH | LD82PH | ld8 2ph | ld82ph | Powys | Powys | Old Radnor STW | 1157 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 325792 | 259505 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PL | LD82PL | ld8 2pl | ld82pl | Powys | Powys | Old Radnor STW | 1161 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 325701 | 258929 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PN | LD82PN | ld8 2pn | ld82pn | Powys | Powys | Old Radnor STW | 1033 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 325240 | 258559 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PP | LD82PP | ld8 2pp | ld82pp | Powys | Powys | Old Radnor STW | 2175 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 324495 | 257231 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PT | LD82PT | ld8 2pt | ld82pt | Powys | Powys | Evenjobb STW | 1768 | 953 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.76 | 9.47 | 10.47 | 326582 | 260517 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PU | LD82PU | ld8 2pu | ld82pu | Powys | Powys | Old Radnor STW | 1906 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 326462 | 259957 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PW | LD82PW | ld8 2pw | ld82pw | Powys | Powys | Old Radnor STW | 1217 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 325016 | 258243 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2PY | LD82PY | ld8 2py | ld82py | Powys | Powys | Old Radnor STW | 1031 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 325589 | 259801 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RA | LD82RA | ld8 2ra | ld82ra | Powys | Powys | Old Radnor STW | 1379 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 324608 | 260778 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RB | LD82RB | ld8 2rb | ld82rb | Powys | Powys | Old Radnor STW | 590 | 996 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.56 | 9.9 | 10.94 | 324610 | 259989 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RD | LD82RD | ld8 2rd | ld82rd | Powys | Powys | New Radnor STW | 1276 | 1055 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.66 | 10.49 | 11.59 | 323074 | 260605 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RE | LD82RE | ld8 2re | ld82re | Powys | Powys | Old Radnor STW | 1472 | 1046 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.5 | 10.4 | 11.49 | 323169 | 259424 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RF | LD82RF | ld8 2rf | ld82rf | Powys | Powys | Old Radnor STW | 960 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 325541 | 259730 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RG | LD82RG | ld8 2rg | ld82rg | Powys | Powys | Old Radnor STW | 526 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 325151 | 259277 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RH | LD82RH | ld8 2rh | ld82rh | Powys | Powys | Old Radnor STW | 406 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 324896 | 259085 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RJ | LD82RJ | ld8 2rj | ld82rj | Powys | Powys | Presteigne STW | 555 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331687 | 264260 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RL | LD82RL | ld8 2rl | ld82rl | Powys | Powys | Old Radnor STW | 605 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 324967 | 258891 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RN | LD82RN | ld8 2rn | ld82rn | Powys | Powys | Old Radnor STW | 1313 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 324615 | 258088 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RP | LD82RP | ld8 2rp | ld82rp | Powys | Powys | New Radnor STW | 2969 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 321907 | 257788 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RR | LD82RR | ld8 2rr | ld82rr | Powys | Powys | Old Radnor STW | 2218 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 323784 | 257355 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RS | LD82RS | ld8 2rs | ld82rs | Powys | Powys | Presteigne STW | 2866 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 330441 | 266601 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RT | LD82RT | ld8 2rt | ld82rt | Powys | Powys | Presteigne STW | 619 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331672 | 264101 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RU | LD82RU | ld8 2ru | ld82ru | Powys | Powys | Presteigne STW | 305 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331989 | 264181 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RW | LD82RW | ld8 2rw | ld82rw | Powys | Powys | Old Radnor STW | 1360 | 1004 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.71 | 9.98 | 11.03 | 323843 | 258299 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2RY | LD82RY | ld8 2ry | ld82ry | Powys | Powys | Evenjobb STW | 352 | 1002 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.68 | 9.96 | 11.01 | 326261 | 262609 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SA | LD82SA | ld8 2sa | ld82sa | Powys | Powys | Evenjobb STW | 78 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 326395 | 262338 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SB | LD82SB | ld8 2sb | ld82sb | Powys | Powys | Evenjobb STW | 56 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 326318 | 262310 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SD | LD82SD | ld8 2sd | ld82sd | Powys | Powys | Evenjobb STW | 158 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 326244 | 262381 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SE | LD82SE | ld8 2se | ld82se | Powys | Powys | Evenjobb STW | 1126 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 326678 | 263349 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SF | LD82SF | ld8 2sf | ld82sf | Powys | Powys | Evenjobb STW | 221 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 326525 | 262413 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SG | LD82SG | ld8 2sg | ld82sg | Powys | Powys | Evenjobb STW | 1536 | 998 | 900to1200 | 2 | 1.46 | 1.07 | 18.6 | 9.92 | 10.96 | 327675 | 263057 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SH | LD82SH | ld8 2sh | ld82sh | Powys | Powys | Evenjobb STW | 1723 | 974 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.15 | 9.68 | 10.7 | 327950 | 261614 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SJ | LD82SJ | ld8 2sj | ld82sj | Powys | Powys | Evenjobb STW | 181 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 326324 | 262448 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SL | LD82SL | ld8 2sl | ld82sl | Powys | Powys | New Radnor STW | 658 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321169 | 260914 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SN | LD82SN | ld8 2sn | ld82sn | Powys | Powys | New Radnor STW | 531 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321296 | 260899 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SP | LD82SP | ld8 2sp | ld82sp | Powys | Powys | New Radnor STW | 517 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321292 | 260802 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SQ | LD82SQ | ld8 2sq | ld82sq | Powys | Powys | Evenjobb STW | 193 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 326382 | 262461 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SR | LD82SR | ld8 2sr | ld82sr | Powys | Powys | New Radnor STW | 587 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321221 | 260788 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SS | LD82SS | ld8 2ss | ld82ss | Powys | Powys | New Radnor STW | 288 | 1110 | 900to1200 | 2.22 | 1.63 | 1.19 | 20.69 | 11.03 | 12.2 | 321522 | 260716 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2ST | LD82ST | ld8 2st | ld82st | Powys | Powys | New Radnor STW | 367 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321448 | 260830 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SU | LD82SU | ld8 2su | ld82su | Powys | Powys | New Radnor STW | 496 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321358 | 260964 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SW | LD82SW | ld8 2sw | ld82sw | Powys | Powys | New Radnor STW | 566 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321246 | 260829 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SX | LD82SX | ld8 2sx | ld82sx | Powys | Powys | New Radnor STW | 746 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321061 | 260755 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SY | LD82SY | ld8 2sy | ld82sy | Powys | Powys | New Radnor STW | 445 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321371 | 260840 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2SZ | LD82SZ | ld8 2sz | ld82sz | Powys | Powys | Evenjobb STW | 218 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 326417 | 262480 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TA | LD82TA | ld8 2ta | ld82ta | Powys | Powys | New Radnor STW | 473 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321416 | 261020 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TB | LD82TB | ld8 2tb | ld82tb | Powys | Powys | New Radnor STW | 963 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 320862 | 260937 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TD | LD82TD | ld8 2td | ld82td | Powys | Powys | New Radnor STW | 636 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321187 | 260894 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TE | LD82TE | ld8 2te | ld82te | Powys | Powys | New Radnor STW | 725 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321085 | 260816 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TF | LD82TF | ld8 2tf | ld82tf | Powys | Powys | New Radnor STW | 612 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321202 | 260845 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TG | LD82TG | ld8 2tg | ld82tg | Powys | Powys | New Radnor STW | 1952 | 1061 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.78 | 10.55 | 11.66 | 322886 | 262380 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TH | LD82TH | ld8 2th | ld82th | Powys | Powys | New Radnor STW | 1692 | 1061 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.78 | 10.55 | 11.66 | 322501 | 262296 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TL | LD82TL | ld8 2tl | ld82tl | Powys | Powys | New Radnor STW | 975 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321000 | 261300 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TN | LD82TN | ld8 2tn | ld82tn | Powys | Powys | New Radnor STW | 3306 | 1154 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.51 | 11.47 | 12.68 | 319144 | 258797 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TP | LD82TP | ld8 2tp | ld82tp | Powys | Powys | Llandegley STW | 5499 | 1128 | 900to1200 | 2.26 | 1.65 | 1.21 | 21.02 | 11.21 | 12.39 | 316630 | 258409 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TR | LD82TR | ld8 2tr | ld82tr | Powys | Powys | New Radnor STW | 5255 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 317526 | 257709 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TU | LD82TU | ld8 2tu | ld82tu | Powys | Powys | New Radnor STW | 398 | 1147 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.38 | 11.4 | 12.6 | 321472 | 260968 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2TW | LD82TW | ld8 2tw | ld82tw | Powys | Powys | New Radnor STW | 5107 | 1163 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.68 | 11.56 | 12.78 | 317099 | 258780 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2UA | LD82UA | ld8 2ua | ld82ua | Powys | Powys | Presteigne STW | 2382 | 947 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.65 | 9.41 | 10.4 | 330466 | 265963 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2UB | LD82UB | ld8 2ub | ld82ub | Powys | Powys | Presteigne STW | 3015 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 330368 | 266733 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2UF | LD82UF | ld8 2uf | ld82uf | Powys | Powys | Presteigne STW | 935 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331353 | 264048 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2UG | LD82UG | ld8 2ug | ld82ug | Powys | Powys | Presteigne STW | 807 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331432 | 264263 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2UH | LD82UH | ld8 2uh | ld82uh | Powys | Powys | Presteigne STW | 904 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 331456 | 263901 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2UN | LD82UN | ld8 2un | ld82un | Powys | Powys | Old Radnor STW | 967 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 324950 | 258484 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2WF | LD82WF | ld8 2wf | ld82wf | Powys | Powys | Llanyre WwTW | 1278 | 1063 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.81 | 10.57 | 11.68 | 305975 | 261281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
LD8 2YT | LD82YT | ld8 2yt | ld82yt | Powys | Powys | Presteigne STW | 621 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 331718 | 264017 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
NP15 2DH | NP152DH | np15 2dh | np152dh | Monmouthshire | Sir Fynwy | Penrhos STW | 1251 | 951 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.73 | 9.45 | 10.45 | 340854 | 212611 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LE | NP152LE | np15 2le | np152le | Monmouthshire | Sir Fynwy | Penrhos STW | 329 | 937 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.46 | 9.31 | 10.29 | 341636 | 211839 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LF | NP152LF | np15 2lf | np152lf | Monmouthshire | Sir Fynwy | Penrhos STW | 1230 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 341731 | 212748 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LG | NP152LG | np15 2lg | np152lg | Monmouthshire | Sir Fynwy | Penrhos STW | 187 | 937 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.46 | 9.31 | 10.29 | 341600 | 211698 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LJ | NP152LJ | np15 2lj | np152lj | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 1722 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 339271 | 212891 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LL | NP152LL | np15 2ll | np152ll | Monmouthshire | Sir Fynwy | Penrhos STW | 1611 | 951 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.73 | 9.45 | 10.45 | 340611 | 212883 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP15 2LQ | NP152LQ | np15 2lq | np152lq | Monmouthshire | Sir Fynwy | Penrhos STW | 1678 | 951 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.73 | 9.45 | 10.45 | 341397 | 213214 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AA | NP165AA | np16 5aa | np165aa | Monmouthshire | Sir Fynwy | Tintern STW | 7963 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353511 | 192470 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AB | NP165AB | np16 5ab | np165ab | Monmouthshire | Sir Fynwy | Tintern STW | 7956 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353417 | 192477 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AD | NP165AD | np16 5ad | np165ad | Monmouthshire | Sir Fynwy | Tintern STW | 8112 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353384 | 192322 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AE | NP165AE | np16 5ae | np165ae | Monmouthshire | Sir Fynwy | Tintern STW | 7810 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353349 | 192624 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AF | NP165AF | np16 5af | np165af | Monmouthshire | Sir Fynwy | Tintern STW | 7923 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353318 | 192512 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AG | NP165AG | np16 5ag | np165ag | Monmouthshire | Sir Fynwy | Tintern STW | 8011 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353291 | 192425 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AH | NP165AH | np16 5ah | np165ah | Monmouthshire | Sir Fynwy | Tintern STW | 7982 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353142 | 192459 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AJ | NP165AJ | np16 5aj | np165aj | Monmouthshire | Sir Fynwy | Tintern STW | 7880 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353029 | 192567 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AL | NP165AL | np16 5al | np165al | Monmouthshire | Sir Fynwy | Tintern STW | 7806 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353083 | 192638 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AN | NP165AN | np16 5an | np165an | Monmouthshire | Sir Fynwy | Tintern STW | 7824 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353192 | 192615 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AP | NP165AP | np16 5ap | np165ap | Monmouthshire | Sir Fynwy | Tintern STW | 7868 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353120 | 192574 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AQ | NP165AQ | np16 5aq | np165aq | Monmouthshire | Sir Fynwy | Tintern STW | 7903 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353225 | 192535 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AR | NP165AR | np16 5ar | np165ar | Monmouthshire | Sir Fynwy | Tintern STW | 8149 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353449 | 192284 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AS | NP165AS | np16 5as | np165as | Monmouthshire | Sir Fynwy | Tintern STW | 8078 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353535 | 192355 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AT | NP165AT | np16 5at | np165at | Monmouthshire | Sir Fynwy | Tintern STW | 6665 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352978 | 193788 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AU | NP165AU | np16 5au | np165au | Monmouthshire | Sir Fynwy | Tintern STW | 6654 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352758 | 193820 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AW | NP165AW | np16 5aw | np165aw | Monmouthshire | Sir Fynwy | Tintern STW | 6772 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352924 | 193685 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AX | NP165AX | np16 5ax | np165ax | Monmouthshire | Sir Fynwy | Tintern STW | 6817 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353447 | 193616 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5AY | NP165AY | np16 5ay | np165ay | Monmouthshire | Sir Fynwy | Tintern STW | 6840 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352695 | 193640 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5BH | NP165BH | np16 5bh | np165bh | Monmouthshire | Sir Fynwy | Tintern STW | 7419 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353049 | 193027 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5BL | NP165BL | np16 5bl | np165bl | Monmouthshire | Sir Fynwy | Tintern STW | 6896 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352740 | 193579 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5BN | NP165BN | np16 5bn | np165bn | Monmouthshire | Sir Fynwy | Tintern STW | 6910 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352725 | 193566 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5BP | NP165BP | np16 5bp | np165bp | Monmouthshire | Sir Fynwy | Tintern STW | 6727 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352756 | 193747 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5BR | NP165BR | np16 5br | np165br | Monmouthshire | Sir Fynwy | Tintern STW | 6796 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352882 | 193665 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5BS | NP165BS | np16 5bs | np165bs | Monmouthshire | Sir Fynwy | Tintern STW | 6804 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352986 | 193648 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5BY | NP165BY | np16 5by | np165by | Monmouthshire | Sir Fynwy | Tintern STW | 6743 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353073 | 193703 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5BZ | NP165BZ | np16 5bz | np165bz | Monmouthshire | Sir Fynwy | Tintern STW | 6733 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353406 | 193700 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DA | NP165DA | np16 5da | np165da | Monmouthshire | Sir Fynwy | Tintern STW | 6688 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353223 | 193750 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DB | NP165DB | np16 5db | np165db | Monmouthshire | Sir Fynwy | Tintern STW | 6674 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353264 | 193763 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DD | NP165DD | np16 5dd | np165dd | Monmouthshire | Sir Fynwy | Tintern STW | 6720 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353215 | 193719 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DE | NP165DE | np16 5de | np165de | Monmouthshire | Sir Fynwy | Tintern STW | 6735 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353199 | 193704 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DF | NP165DF | np16 5df | np165df | Monmouthshire | Sir Fynwy | Tintern STW | 6752 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353180 | 193688 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DG | NP165DG | np16 5dg | np165dg | Monmouthshire | Sir Fynwy | Tintern STW | 6777 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353168 | 193664 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DH | NP165DH | np16 5dh | np165dh | Monmouthshire | Sir Fynwy | Tintern STW | 6669 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353195 | 193770 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DJ | NP165DJ | np16 5dj | np165dj | Monmouthshire | Sir Fynwy | Tintern STW | 6844 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353238 | 193594 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DL | NP165DL | np16 5dl | np165dl | Monmouthshire | Sir Fynwy | Tintern STW | 6866 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353388 | 193567 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DN | NP165DN | np16 5dn | np165dn | Monmouthshire | Sir Fynwy | Tintern STW | 6950 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353387 | 193484 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DP | NP165DP | np16 5dp | np165dp | Monmouthshire | Sir Fynwy | Tintern STW | 6940 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 353530 | 193493 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DQ | NP165DQ | np16 5dq | np165dq | Monmouthshire | Sir Fynwy | Tintern STW | 7212 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353407 | 193221 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DR | NP165DR | np16 5dr | np165dr | Monmouthshire | Sir Fynwy | Tintern STW | 6906 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353278 | 193530 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DS | NP165DS | np16 5ds | np165ds | Monmouthshire | Sir Fynwy | Tintern STW | 6985 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353302 | 193450 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DT | NP165DT | np16 5dt | np165dt | Monmouthshire | Sir Fynwy | Tintern STW | 7036 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353293 | 193400 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DU | NP165DU | np16 5du | np165du | Monmouthshire | Sir Fynwy | Tintern STW | 7009 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353244 | 193428 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DW | NP165DW | np16 5dw | np165dw | Monmouthshire | Sir Fynwy | Tintern STW | 7116 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353378 | 193318 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DX | NP165DX | np16 5dx | np165dx | Monmouthshire | Sir Fynwy | Tintern STW | 6969 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353492 | 193464 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DY | NP165DY | np16 5dy | np165dy | Monmouthshire | Sir Fynwy | Tintern STW | 7159 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353454 | 193274 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5DZ | NP165DZ | np16 5dz | np165dz | Monmouthshire | Sir Fynwy | Tintern STW | 7286 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 353627 | 193148 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EA | NP165EA | np16 5ea | np165ea | Monmouthshire | Sir Fynwy | Tintern STW | 7179 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 353506 | 193254 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EB | NP165EB | np16 5eb | np165eb | Monmouthshire | Sir Fynwy | Tintern STW | 7021 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 353502 | 193412 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5ED | NP165ED | np16 5ed | np165ed | Monmouthshire | Sir Fynwy | Tintern STW | 6856 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353288 | 193580 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EE | NP165EE | np16 5ee | np165ee | Monmouthshire | Sir Fynwy | Tintern STW | 7018 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353447 | 193415 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EF | NP165EF | np16 5ef | np165ef | Monmouthshire | Sir Fynwy | Tintern STW | 6781 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353315 | 193654 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EG | NP165EG | np16 5eg | np165eg | Monmouthshire | Sir Fynwy | Tintern STW | 6961 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352740 | 193513 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EJ | NP165EJ | np16 5ej | np165ej | Monmouthshire | Sir Fynwy | Tintern STW | 6518 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353325 | 193917 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EL | NP165EL | np16 5el | np165el | Monmouthshire | Sir Fynwy | Tintern STW | 6604 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353297 | 193832 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EN | NP165EN | np16 5en | np165en | Monmouthshire | Sir Fynwy | Tintern STW | 6539 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353345 | 193895 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EP | NP165EP | np16 5ep | np165ep | Monmouthshire | Sir Fynwy | Tintern STW | 6492 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353381 | 193942 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EQ | NP165EQ | np16 5eq | np165eq | Monmouthshire | Sir Fynwy | Tintern STW | 6387 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353495 | 194045 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5ER | NP165ER | np16 5er | np165er | Monmouthshire | Sir Fynwy | Tintern STW | 6446 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353418 | 193987 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5ES | NP165ES | np16 5es | np165es | Monmouthshire | Sir Fynwy | Tintern STW | 6410 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353434 | 194023 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5ET | NP165ET | np16 5et | np165et | Monmouthshire | Sir Fynwy | Tintern STW | 6454 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353442 | 193979 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EU | NP165EU | np16 5eu | np165eu | Monmouthshire | Sir Fynwy | Tintern STW | 6498 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353458 | 193935 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EW | NP165EW | np16 5ew | np165ew | Monmouthshire | Sir Fynwy | Tintern STW | 6460 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353477 | 193972 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EX | NP165EX | np16 5ex | np165ex | Monmouthshire | Sir Fynwy | Tintern STW | 6448 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353497 | 193984 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EY | NP165EY | np16 5ey | np165ey | Monmouthshire | Sir Fynwy | Tintern STW | 6321 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353489 | 194111 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5EZ | NP165EZ | np16 5ez | np165ez | Monmouthshire | Sir Fynwy | Tintern STW | 6192 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353592 | 194241 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5FA | NP165FA | np16 5fa | np165fa | Monmouthshire | Sir Fynwy | Tintern STW | 8788 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 354097 | 191666 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5FB | NP165FB | np16 5fb | np165fb | Monmouthshire | Sir Fynwy | Tintern STW | 6914 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352786 | 193556 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5FE | NP165FE | np16 5fe | np165fe | Monmouthshire | Sir Fynwy | Tintern STW | 6590 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353322 | 193845 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5FF | NP165FF | np16 5ff | np165ff | Monmouthshire | Sir Fynwy | Tintern STW | 6975 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353070 | 193471 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5FG | NP165FG | np16 5fg | np165fg | Monmouthshire | Sir Fynwy | Tintern STW | 6288 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353812 | 194152 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5FH | NP165FH | np16 5fh | np165fh | Monmouthshire | Sir Fynwy | Tintern STW | 6340 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353833 | 194101 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5FJ | NP165FJ | np16 5fj | np165fj | Monmouthshire | Sir Fynwy | Tintern STW | 6321 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353729 | 194116 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5FN | NP165FN | np16 5fn | np165fn | Monmouthshire | Sir Fynwy | Tintern STW | 6821 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353378 | 193613 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5FP | NP165FP | np16 5fp | np165fp | Monmouthshire | Sir Fynwy | Tintern STW | 7844 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353280 | 192592 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5FQ | NP165FQ | np16 5fq | np165fq | Monmouthshire | Sir Fynwy | Tintern STW | 6148 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353651 | 194286 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5FY | NP165FY | np16 5fy | np165fy | Monmouthshire | Sir Fynwy | Tintern STW | 6228 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353758 | 194210 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5GB | NP165GB | np16 5gb | np165gb | Monmouthshire | Sir Fynwy | Tintern STW | 8808 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353874 | 191633 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5GE | NP165GE | np16 5ge | np165ge | Monmouthshire | Sir Fynwy | Tintern STW | 8905 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353889 | 191537 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5GF | NP165GF | np16 5gf | np165gf | Monmouthshire | Sir Fynwy | Tintern STW | 8928 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353959 | 191517 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5GH | NP165GH | np16 5gh | np165gh | Monmouthshire | Sir Fynwy | Tintern STW | 8859 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353939 | 191585 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HA | NP165HA | np16 5ha | np165ha | Monmouthshire | Sir Fynwy | Tintern STW | 6426 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353496 | 194006 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HB | NP165HB | np16 5hb | np165hb | Monmouthshire | Sir Fynwy | Tintern STW | 6323 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353516 | 194109 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HD | NP165HD | np16 5hd | np165hd | Monmouthshire | Sir Fynwy | Tintern STW | 6211 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353553 | 194222 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HE | NP165HE | np16 5he | np165he | Monmouthshire | Sir Fynwy | Tintern STW | 6218 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353665 | 194217 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HF | NP165HF | np16 5hf | np165hf | Monmouthshire | Sir Fynwy | Tintern STW | 6186 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353656 | 194248 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HH | NP165HH | np16 5hh | np165hh | Monmouthshire | Sir Fynwy | Tintern STW | 6199 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353736 | 194238 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HJ | NP165HJ | np16 5hj | np165hj | Monmouthshire | Sir Fynwy | Tintern STW | 6330 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353692 | 194105 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HL | NP165HL | np16 5hl | np165hl | Monmouthshire | Sir Fynwy | Tintern STW | 6373 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353679 | 194062 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HN | NP165HN | np16 5hn | np165hn | Monmouthshire | Sir Fynwy | Tintern STW | 6415 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353643 | 194019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HP | NP165HP | np16 5hp | np165hp | Monmouthshire | Sir Fynwy | Tintern STW | 6366 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353611 | 194067 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HQ | NP165HQ | np16 5hq | np165hq | Monmouthshire | Sir Fynwy | Tintern STW | 6229 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353617 | 194204 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HR | NP165HR | np16 5hr | np165hr | Monmouthshire | Sir Fynwy | Tintern STW | 6398 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353548 | 194035 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HS | NP165HS | np16 5hs | np165hs | Monmouthshire | Sir Fynwy | Tintern STW | 6245 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353791 | 194194 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HT | NP165HT | np16 5ht | np165ht | Monmouthshire | Sir Fynwy | Tintern STW | 6518 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353468 | 193915 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HU | NP165HU | np16 5hu | np165hu | Monmouthshire | Sir Fynwy | Tintern STW | 6443 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353531 | 193989 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HW | NP165HW | np16 5hw | np165hw | Monmouthshire | Sir Fynwy | Tintern STW | 6400 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353683 | 194035 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HX | NP165HX | np16 5hx | np165hx | Monmouthshire | Sir Fynwy | Tintern STW | 6310 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353630 | 194124 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HY | NP165HY | np16 5hy | np165hy | Monmouthshire | Sir Fynwy | Tintern STW | 6355 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353565 | 194078 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5HZ | NP165HZ | np16 5hz | np165hz | Monmouthshire | Sir Fynwy | Tintern STW | 6575 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353281 | 193861 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JA | NP165JA | np16 5ja | np165ja | Monmouthshire | Sir Fynwy | Tintern STW | 6508 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353220 | 193930 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JD | NP165JD | np16 5jd | np165jd | Monmouthshire | Sir Fynwy | Tintern STW | 7338 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353074 | 193107 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JE | NP165JE | np16 5je | np165je | Monmouthshire | Sir Fynwy | Tintern STW | 7125 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353145 | 193317 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JF | NP165JF | np16 5jf | np165jf | Monmouthshire | Sir Fynwy | Tintern STW | 7346 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353185 | 193093 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JG | NP165JG | np16 5jg | np165jg | Monmouthshire | Sir Fynwy | Tintern STW | 7344 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353244 | 193093 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JH | NP165JH | np16 5jh | np165jh | Monmouthshire | Sir Fynwy | Tintern STW | 7213 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353006 | 193237 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JJ | NP165JJ | np16 5jj | np165jj | Monmouthshire | Sir Fynwy | Tintern STW | 7411 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353150 | 193030 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JL | NP165JL | np16 5jl | np165jl | Monmouthshire | Sir Fynwy | Tintern STW | 7301 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353173 | 193139 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JN | NP165JN | np16 5jn | np165jn | Monmouthshire | Sir Fynwy | Tintern STW | 7636 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353349 | 192798 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JP | NP165JP | np16 5jp | np165jp | Monmouthshire | Sir Fynwy | Tintern STW | 7614 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353267 | 192822 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JQ | NP165JQ | np16 5jq | np165jq | Monmouthshire | Sir Fynwy | Tintern STW | 7484 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353339 | 192951 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JR | NP165JR | np16 5jr | np165jr | Monmouthshire | Sir Fynwy | Tintern STW | 7518 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353266 | 192918 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JS | NP165JS | np16 5js | np165js | Monmouthshire | Sir Fynwy | Tintern STW | 7430 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353205 | 193009 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JT | NP165JT | np16 5jt | np165jt | Monmouthshire | Sir Fynwy | Tintern STW | 7472 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353133 | 192970 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JU | NP165JU | np16 5ju | np165ju | Monmouthshire | Sir Fynwy | Tintern STW | 7453 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353392 | 192981 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JW | NP165JW | np16 5jw | np165jw | Monmouthshire | Sir Fynwy | Tintern STW | 7723 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353419 | 192710 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JX | NP165JX | np16 5jx | np165jx | Monmouthshire | Sir Fynwy | Tintern STW | 7529 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353391 | 192905 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JY | NP165JY | np16 5jy | np165jy | Monmouthshire | Sir Fynwy | Tintern STW | 7508 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353494 | 192925 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5JZ | NP165JZ | np16 5jz | np165jz | Monmouthshire | Sir Fynwy | Tintern STW | 7304 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353311 | 193131 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LA | NP165LA | np16 5la | np165la | Monmouthshire | Sir Fynwy | Tintern STW | 7278 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353382 | 193156 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LD | NP165LD | np16 5ld | np165ld | Monmouthshire | Sir Fynwy | Tintern STW | 7352 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353394 | 193082 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LE | NP165LE | np16 5le | np165le | Monmouthshire | Sir Fynwy | Tintern STW | 6162 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352532 | 194347 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LF | NP165LF | np16 5lf | np165lf | Monmouthshire | Sir Fynwy | Tintern STW | 6311 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352820 | 194158 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LG | NP165LG | np16 5lg | np165lg | Monmouthshire | Sir Fynwy | Tintern STW | 6498 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353424 | 193935 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LH | NP165LH | np16 5lh | np165lh | Monmouthshire | Sir Fynwy | Tintern STW | 6642 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353323 | 193793 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LJ | NP165LJ | np16 5lj | np165lj | Monmouthshire | Sir Fynwy | Tintern STW | 6596 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353319 | 193839 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LL | NP165LL | np16 5ll | np165ll | Monmouthshire | Sir Fynwy | Tintern STW | 6626 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353251 | 193811 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LN | NP165LN | np16 5ln | np165ln | Monmouthshire | Sir Fynwy | Tintern STW | 6583 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353159 | 193858 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LP | NP165LP | np16 5lp | np165lp | Monmouthshire | Sir Fynwy | Tintern STW | 6557 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353103 | 193887 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LQ | NP165LQ | np16 5lq | np165lq | Monmouthshire | Sir Fynwy | Tintern STW | 6592 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353384 | 193841 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LR | NP165LR | np16 5lr | np165lr | Monmouthshire | Sir Fynwy | Tintern STW | 6481 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353063 | 193966 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LS | NP165LS | np16 5ls | np165ls | Monmouthshire | Sir Fynwy | Tintern STW | 6271 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352914 | 194189 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LT | NP165LT | np16 5lt | np165lt | Monmouthshire | Sir Fynwy | Tintern STW | 6201 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352926 | 194258 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LU | NP165LU | np16 5lu | np165lu | Monmouthshire | Sir Fynwy | Tintern STW | 6112 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352733 | 194369 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LY | NP165LY | np16 5ly | np165ly | Monmouthshire | Sir Fynwy | Tintern STW | 6327 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352757 | 194149 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5LZ | NP165LZ | np16 5lz | np165lz | Monmouthshire | Sir Fynwy | Tintern STW | 6275 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352545 | 194230 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NA | NP165NA | np16 5na | np165na | Monmouthshire | Sir Fynwy | Tintern STW | 6202 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 352494 | 194312 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NB | NP165NB | np16 5nb | np165nb | Monmouthshire | Sir Fynwy | Tintern STW | 6280 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352620 | 194214 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5ND | NP165ND | np16 5nd | np165nd | Monmouthshire | Sir Fynwy | Tintern STW | 6274 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352724 | 194207 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NE | NP165NE | np16 5ne | np165ne | Monmouthshire | Sir Fynwy | Tintern STW | 6473 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352646 | 194016 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NF | NP165NF | np16 5nf | np165nf | Monmouthshire | Sir Fynwy | Tintern STW | 6476 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352927 | 193982 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NG | NP165NG | np16 5ng | np165ng | Monmouthshire | Sir Fynwy | Tintern STW | 8354 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353425 | 192079 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NH | NP165NH | np16 5nh | np165nh | Monmouthshire | Sir Fynwy | Tintern STW | 8271 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353416 | 192163 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NJ | NP165NJ | np16 5nj | np165nj | Monmouthshire | Sir Fynwy | Tintern STW | 8248 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353509 | 192185 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NL | NP165NL | np16 5nl | np165nl | Monmouthshire | Sir Fynwy | Tintern STW | 8302 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353556 | 192131 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NN | NP165NN | np16 5nn | np165nn | Monmouthshire | Sir Fynwy | Tintern STW | 8398 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353509 | 192035 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NP | NP165NP | np16 5np | np165np | Monmouthshire | Sir Fynwy | Tintern STW | 8417 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353608 | 192017 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NQ | NP165NQ | np16 5nq | np165nq | Monmouthshire | Sir Fynwy | Tintern STW | 8382 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353371 | 192052 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NR | NP165NR | np16 5nr | np165nr | Monmouthshire | Sir Fynwy | Tintern STW | 8523 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353634 | 191911 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NS | NP165NS | np16 5ns | np165ns | Monmouthshire | Sir Fynwy | Tintern STW | 8206 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353626 | 192228 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NT | NP165NT | np16 5nt | np165nt | Monmouthshire | Sir Fynwy | Tintern STW | 8382 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353672 | 192053 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NU | NP165NU | np16 5nu | np165nu | Monmouthshire | Sir Fynwy | Tintern STW | 6370 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352688 | 194114 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NW | NP165NW | np16 5nw | np165nw | Monmouthshire | Sir Fynwy | Tintern STW | 8508 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353575 | 191925 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NX | NP165NX | np16 5nx | np165nx | Monmouthshire | Sir Fynwy | Tintern STW | 8245 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353727 | 192191 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NY | NP165NY | np16 5ny | np165ny | Monmouthshire | Sir Fynwy | Tintern STW | 8307 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353751 | 192130 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5NZ | NP165NZ | np16 5nz | np165nz | Monmouthshire | Sir Fynwy | Tintern STW | 6211 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352881 | 194252 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PA | NP165PA | np16 5pa | np165pa | Monmouthshire | Sir Fynwy | Tintern STW | 6620 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353490 | 193812 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PB | NP165PB | np16 5pb | np165pb | Monmouthshire | Sir Fynwy | Tintern STW | 6729 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353598 | 193704 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PD | NP165PD | np16 5pd | np165pd | Monmouthshire | Sir Fynwy | Tintern STW | 6764 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353603 | 193669 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PE | NP165PE | np16 5pe | np165pe | Monmouthshire | Sir Fynwy | Tintern STW | 6744 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353487 | 193689 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PF | NP165PF | np16 5pf | np165pf | Monmouthshire | Sir Fynwy | Tintern STW | 6814 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353582 | 193619 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PG | NP165PG | np16 5pg | np165pg | Monmouthshire | Sir Fynwy | Tintern STW | 6619 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353395 | 193814 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PH | NP165PH | np16 5ph | np165ph | Monmouthshire | Sir Fynwy | Tintern STW | 6651 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353474 | 193782 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PJ | NP165PJ | np16 5pj | np165pj | Monmouthshire | Sir Fynwy | Tintern STW | 6845 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353102 | 193599 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PL | NP165PL | np16 5pl | np165pl | Monmouthshire | Sir Fynwy | Tintern STW | 6846 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353048 | 193601 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PN | NP165PN | np16 5pn | np165pn | Monmouthshire | Sir Fynwy | Tintern STW | 7036 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 352979 | 193416 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PP | NP165PP | np16 5pp | np165pp | Monmouthshire | Sir Fynwy | Tintern STW | 6943 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353020 | 193506 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PQ | NP165PQ | np16 5pq | np165pq | Monmouthshire | Sir Fynwy | Tintern STW | 6639 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353377 | 193795 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PR | NP165PR | np16 5pr | np165pr | Monmouthshire | Sir Fynwy | Tintern STW | 7209 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 352879 | 193250 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PS | NP165PS | np16 5ps | np165ps | Monmouthshire | Sir Fynwy | Tintern STW | 6817 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353129 | 193626 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PT | NP165PT | np16 5pt | np165pt | Monmouthshire | Sir Fynwy | Tintern STW | 6943 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353126 | 193500 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PU | NP165PU | np16 5pu | np165pu | Monmouthshire | Sir Fynwy | Tintern STW | 6868 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353169 | 193573 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PW | NP165PW | np16 5pw | np165pw | Monmouthshire | Sir Fynwy | Tintern STW | 7072 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 352938 | 193383 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PX | NP165PX | np16 5px | np165px | Monmouthshire | Sir Fynwy | Tintern STW | 6913 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352927 | 193543 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PY | NP165PY | np16 5py | np165py | Monmouthshire | Sir Fynwy | Tintern STW | 6974 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 352865 | 193488 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5PZ | NP165PZ | np16 5pz | np165pz | Monmouthshire | Sir Fynwy | Tintern STW | 6871 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352958 | 193583 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QA | NP165QA | np16 5qa | np165qa | Monmouthshire | Sir Fynwy | Tintern STW | 6278 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352670 | 194209 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QB | NP165QB | np16 5qb | np165qb | Monmouthshire | Sir Fynwy | Tintern STW | 6835 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353073 | 193611 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QD | NP165QD | np16 5qd | np165qd | Monmouthshire | Sir Fynwy | Tintern STW | 6494 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353890 | 193950 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QE | NP165QE | np16 5qe | np165qe | Monmouthshire | Sir Fynwy | Tintern STW | 7849 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353496 | 192584 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QF | NP165QF | np16 5qf | np165qf | Monmouthshire | Sir Fynwy | Tintern STW | 8263 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353820 | 192176 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QG | NP165QG | np16 5qg | np165qg | Monmouthshire | Sir Fynwy | Tintern STW | 7911 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 353593 | 192522 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QH | NP165QH | np16 5qh | np165qh | Monmouthshire | Sir Fynwy | Tintern STW | 8014 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353597 | 192420 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QJ | NP165QJ | np16 5qj | np165qj | Monmouthshire | Sir Fynwy | Tintern STW | 7967 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353699 | 192468 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QL | NP165QL | np16 5ql | np165ql | Monmouthshire | Sir Fynwy | Tintern STW | 7962 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353855 | 192479 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QN | NP165QN | np16 5qn | np165qn | Monmouthshire | Sir Fynwy | Tintern STW | 8067 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353646 | 192367 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QP | NP165QP | np16 5qp | np165qp | Monmouthshire | Sir Fynwy | Tintern STW | 8145 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353780 | 192293 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QQ | NP165QQ | np16 5qq | np165qq | Monmouthshire | Sir Fynwy | Tintern STW | 8006 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353751 | 192431 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QR | NP165QR | np16 5qr | np165qr | Monmouthshire | Sir Fynwy | Tintern STW | 7951 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353783 | 192487 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QS | NP165QS | np16 5qs | np165qs | Monmouthshire | Sir Fynwy | Tintern STW | 8148 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353702 | 192288 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QT | NP165QT | np16 5qt | np165qt | Monmouthshire | Sir Fynwy | Tintern STW | 7820 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 353716 | 192616 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QU | NP165QU | np16 5qu | np165qu | Monmouthshire | Sir Fynwy | Tintern STW | 7846 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 353628 | 192588 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QW | NP165QW | np16 5qw | np165qw | Monmouthshire | Sir Fynwy | Tintern STW | 7892 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 353778 | 192546 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QX | NP165QX | np16 5qx | np165qx | Monmouthshire | Sir Fynwy | Tintern STW | 7782 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 353604 | 192652 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QY | NP165QY | np16 5qy | np165qy | Monmouthshire | Sir Fynwy | Tintern STW | 7175 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 352921 | 193281 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5QZ | NP165QZ | np16 5qz | np165qz | Monmouthshire | Sir Fynwy | Tintern STW | 7682 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 353553 | 192751 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RA | NP165RA | np16 5ra | np165ra | Monmouthshire | Sir Fynwy | Tintern STW | 7915 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 353002 | 192534 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RB | NP165RB | np16 5rb | np165rb | Monmouthshire | Sir Fynwy | Tintern STW | 7957 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353041 | 192489 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RD | NP165RD | np16 5rd | np165rd | Monmouthshire | Sir Fynwy | Tintern STW | 8023 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353080 | 192421 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RE | NP165RE | np16 5re | np165re | Monmouthshire | Sir Fynwy | Tintern STW | 8045 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353107 | 192398 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RF | NP165RF | np16 5rf | np165rf | Monmouthshire | Sir Fynwy | Tintern STW | 8146 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353235 | 192291 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RG | NP165RG | np16 5rg | np165rg | Monmouthshire | Sir Fynwy | Tintern STW | 8104 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353096 | 192339 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RH | NP165RH | np16 5rh | np165rh | Monmouthshire | Sir Fynwy | Tintern STW | 8095 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353161 | 192345 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RJ | NP165RJ | np16 5rj | np165rj | Monmouthshire | Sir Fynwy | Tintern STW | 8136 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353176 | 192303 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RL | NP165RL | np16 5rl | np165rl | Monmouthshire | Sir Fynwy | Tintern STW | 8171 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353176 | 192268 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RN | NP165RN | np16 5rn | np165rn | Monmouthshire | Sir Fynwy | Tintern STW | 8249 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353229 | 192189 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RP | NP165RP | np16 5rp | np165rp | Monmouthshire | Sir Fynwy | Tintern STW | 8392 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353301 | 192043 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RQ | NP165RQ | np16 5rq | np165rq | Monmouthshire | Sir Fynwy | Tintern STW | 8279 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353302 | 192156 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RR | NP165RR | np16 5rr | np165rr | Monmouthshire | Sir Fynwy | Tintern STW | 8245 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353269 | 192191 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RS | NP165RS | np16 5rs | np165rs | Monmouthshire | Sir Fynwy | Tintern STW | 8455 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353343 | 191980 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RT | NP165RT | np16 5rt | np165rt | Monmouthshire | Sir Fynwy | Tintern STW | 8507 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 353442 | 191926 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RU | NP165RU | np16 5ru | np165ru | Monmouthshire | Sir Fynwy | Tintern STW | 8639 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353664 | 191796 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RW | NP165RW | np16 5rw | np165rw | Monmouthshire | Sir Fynwy | Tintern STW | 8644 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353712 | 191792 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RX | NP165RX | np16 5rx | np165rx | Monmouthshire | Sir Fynwy | Tintern STW | 8518 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353778 | 191920 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RY | NP165RY | np16 5ry | np165ry | Monmouthshire | Sir Fynwy | Tintern STW | 8556 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353790 | 191882 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5RZ | NP165RZ | np16 5rz | np165rz | Monmouthshire | Sir Fynwy | Tintern STW | 8503 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353867 | 191938 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SA | NP165SA | np16 5sa | np165sa | Monmouthshire | Sir Fynwy | Tintern STW | 6552 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352664 | 193934 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SB | NP165SB | np16 5sb | np165sb | Monmouthshire | Sir Fynwy | Tintern STW | 6531 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352717 | 193949 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SD | NP165SD | np16 5sd | np165sd | Monmouthshire | Sir Fynwy | Tintern STW | 6467 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 352454 | 194051 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SE | NP165SE | np16 5se | np165se | Monmouthshire | Sir Fynwy | Tintern STW | 6418 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352539 | 194087 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SF | NP165SF | np16 5sf | np165sf | Monmouthshire | Sir Fynwy | Tintern STW | 6487 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 352468 | 194028 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SG | NP165SG | np16 5sg | np165sg | Monmouthshire | Sir Fynwy | Tintern STW | 6457 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352585 | 194041 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SH | NP165SH | np16 5sh | np165sh | Monmouthshire | Sir Fynwy | Tintern STW | 8462 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353906 | 191981 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SJ | NP165SJ | np16 5sj | np165sj | Monmouthshire | Sir Fynwy | Tintern STW | 6479 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352677 | 194006 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SL | NP165SL | np16 5sl | np165sl | Monmouthshire | Sir Fynwy | Tintern STW | 6606 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352828 | 193861 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SN | NP165SN | np16 5sn | np165sn | Monmouthshire | Sir Fynwy | Tintern STW | 6576 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352947 | 193880 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SP | NP165SP | np16 5sp | np165sp | Monmouthshire | Sir Fynwy | Tintern STW | 8443 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353864 | 191998 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SQ | NP165SQ | np16 5sq | np165sq | Monmouthshire | Sir Fynwy | Tintern STW | 8771 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353848 | 191669 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SR | NP165SR | np16 5sr | np165sr | Monmouthshire | Sir Fynwy | Tintern STW | 8614 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 354118 | 191841 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SS | NP165SS | np16 5ss | np165ss | Monmouthshire | Sir Fynwy | Tintern STW | 8646 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 354145 | 191811 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5ST | NP165ST | np16 5st | np165st | Monmouthshire | Sir Fynwy | Tintern STW | 8556 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 354139 | 191901 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SU | NP165SU | np16 5su | np165su | Monmouthshire | Sir Fynwy | Tintern STW | 8468 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 354112 | 191987 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SW | NP165SW | np16 5sw | np165sw | Monmouthshire | Sir Fynwy | Tintern STW | 8693 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 354046 | 191757 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SX | NP165SX | np16 5sx | np165sx | Monmouthshire | Sir Fynwy | Tintern STW | 8614 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 354015 | 191835 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SY | NP165SY | np16 5sy | np165sy | Monmouthshire | Sir Fynwy | Tintern STW | 8606 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 354050 | 191845 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5SZ | NP165SZ | np16 5sz | np165sz | Monmouthshire | Sir Fynwy | Tintern STW | 8737 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353913 | 191706 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TA | NP165TA | np16 5ta | np165ta | Monmouthshire | Sir Fynwy | Tintern STW | 8664 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353955 | 191781 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TB | NP165TB | np16 5tb | np165tb | Monmouthshire | Sir Fynwy | Tintern STW | 8669 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353909 | 191774 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TD | NP165TD | np16 5td | np165td | Monmouthshire | Sir Fynwy | Tintern STW | 8641 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353866 | 191800 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TE | NP165TE | np16 5te | np165te | Monmouthshire | Sir Fynwy | Tintern STW | 8546 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353931 | 191898 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TF | NP165TF | np16 5tf | np165tf | Monmouthshire | Sir Fynwy | Tintern STW | 8348 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353966 | 192098 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TG | NP165TG | np16 5tg | np165tg | Monmouthshire | Sir Fynwy | Tintern STW | 8350 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353905 | 192093 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TH | NP165TH | np16 5th | np165th | Monmouthshire | Sir Fynwy | Tintern STW | 8539 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 354026 | 191910 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TJ | NP165TJ | np16 5tj | np165tj | Monmouthshire | Sir Fynwy | Tintern STW | 8424 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 354027 | 192026 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TL | NP165TL | np16 5tl | np165tl | Monmouthshire | Sir Fynwy | Tintern STW | 8480 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 354057 | 191971 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TN | NP165TN | np16 5tn | np165tn | Monmouthshire | Sir Fynwy | Tintern STW | 6620 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 352301 | 193922 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TP | NP165TP | np16 5tp | np165tp | Monmouthshire | Sir Fynwy | Tintern STW | 8096 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353913 | 192348 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TQ | NP165TQ | np16 5tq | np165tq | Monmouthshire | Sir Fynwy | Tintern STW | 8719 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353852 | 191721 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TR | NP165TR | np16 5tr | np165tr | Monmouthshire | Sir Fynwy | Tintern STW | 8317 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353849 | 192123 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TS | NP165TS | np16 5ts | np165ts | Monmouthshire | Sir Fynwy | Tintern STW | 8209 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353881 | 192233 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TT | NP165TT | np16 5tt | np165tt | Monmouthshire | Sir Fynwy | Tintern STW | 8154 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353851 | 192287 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TU | NP165TU | np16 5tu | np165tu | Monmouthshire | Sir Fynwy | Tintern STW | 8069 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353869 | 192372 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TW | NP165TW | np16 5tw | np165tw | Monmouthshire | Sir Fynwy | Tintern STW | 6630 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 352259 | 193920 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TX | NP165TX | np16 5tx | np165tx | Monmouthshire | Sir Fynwy | Tintern STW | 6445 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 352350 | 194091 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TY | NP165TY | np16 5ty | np165ty | Monmouthshire | Sir Fynwy | Tintern STW | 8703 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353827 | 191736 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5TZ | NP165TZ | np16 5tz | np165tz | Monmouthshire | Sir Fynwy | Tintern STW | 6619 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 352365 | 193912 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UD | NP165UD | np16 5ud | np165ud | Monmouthshire | Sir Fynwy | Tintern STW | 8136 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353508 | 192297 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UE | NP165UE | np16 5ue | np165ue | Monmouthshire | Sir Fynwy | Tintern STW | 6016 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352588 | 194486 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UF | NP165UF | np16 5uf | np165uf | Monmouthshire | Sir Fynwy | Tintern STW | 7113 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 352896 | 193345 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UG | NP165UG | np16 5ug | np165ug | Monmouthshire | Sir Fynwy | Tintern STW | 6729 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 352351 | 193802 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UH | NP165UH | np16 5uh | np165uh | Monmouthshire | Sir Fynwy | Tintern STW | 8766 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353735 | 191670 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UJ | NP165UJ | np16 5uj | np165uj | Monmouthshire | Sir Fynwy | Tintern STW | 6407 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 352922 | 194052 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UL | NP165UL | np16 5ul | np165ul | Monmouthshire | Sir Fynwy | Tintern STW | 6692 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353600 | 193741 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UN | NP165UN | np16 5un | np165un | Monmouthshire | Sir Fynwy | Tintern STW | 6797 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353724 | 193639 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UP | NP165UP | np16 5up | np165up | Monmouthshire | Sir Fynwy | Tintern STW | 8676 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353598 | 191758 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UQ | NP165UQ | np16 5uq | np165uq | Monmouthshire | Sir Fynwy | Tintern STW | 6392 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353095 | 194053 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UR | NP165UR | np16 5ur | np165ur | Monmouthshire | Sir Fynwy | Tintern STW | 6852 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353753 | 193585 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5US | NP165US | np16 5us | np165us | Monmouthshire | Sir Fynwy | Tintern STW | 7012 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 353758 | 193425 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UT | NP165UT | np16 5ut | np165ut | Monmouthshire | Sir Fynwy | Tintern STW | 6608 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353734 | 193829 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UU | NP165UU | np16 5uu | np165uu | Monmouthshire | Sir Fynwy | Tintern STW | 6782 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353805 | 193657 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UW | NP165UW | np16 5uw | np165uw | Monmouthshire | Sir Fynwy | Tintern STW | 6516 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353079 | 193930 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UX | NP165UX | np16 5ux | np165ux | Monmouthshire | Sir Fynwy | Tintern STW | 6677 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353888 | 193767 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UY | NP165UY | np16 5uy | np165uy | Monmouthshire | Sir Fynwy | Tintern STW | 6687 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353752 | 193750 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5UZ | NP165UZ | np16 5uz | np165uz | Monmouthshire | Sir Fynwy | Tintern STW | 6670 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353529 | 193763 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5WB | NP165WB | np16 5wb | np165wb | Monmouthshire | Sir Fynwy | Tintern STW | 6712 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353806 | 193727 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5WE | NP165WE | np16 5we | np165we | Monmouthshire | Sir Fynwy | Tintern STW | 6603 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353891 | 193841 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5WF | NP165WF | np16 5wf | np165wf | Monmouthshire | Sir Fynwy | Tintern STW | 6693 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353850 | 193749 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5WG | NP165WG | np16 5wg | np165wg | Monmouthshire | Sir Fynwy | Tintern STW | 6885 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353703 | 193551 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5WH | NP165WH | np16 5wh | np165wh | Monmouthshire | Sir Fynwy | Tintern STW | 6810 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353835 | 193631 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5WJ | NP165WJ | np16 5wj | np165wj | Monmouthshire | Sir Fynwy | Tintern STW | 7087 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 353682 | 193348 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5XA | NP165XA | np16 5xa | np165xa | Monmouthshire | Sir Fynwy | Tintern STW | 6670 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353529 | 193763 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5XG | NP165XG | np16 5xg | np165xg | Monmouthshire | Sir Fynwy | Tintern STW | 6586 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353209 | 193853 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5XJ | NP165XJ | np16 5xj | np165xj | Monmouthshire | Sir Fynwy | Tintern STW | 6498 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353373 | 193936 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5XQ | NP165XQ | np16 5xq | np165xq | Monmouthshire | Sir Fynwy | Tintern STW | 6546 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353362 | 193888 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5XW | NP165XW | np16 5xw | np165xw | Monmouthshire | Sir Fynwy | Tintern STW | 6717 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353237 | 193721 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5XX | NP165XX | np16 5xx | np165xx | Monmouthshire | Sir Fynwy | Tintern STW | 6608 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353336 | 193826 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5XY | NP165XY | np16 5xy | np165xy | Monmouthshire | Sir Fynwy | Tintern STW | 6607 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 353356 | 193827 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5YE | NP165YE | np16 5ye | np165ye | Monmouthshire | Sir Fynwy | Tintern STW | 6670 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353529 | 193763 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 5ZN | NP165ZN | np16 5zn | np165zn | Monmouthshire | Sir Fynwy | Tintern STW | 8339 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353551 | 192094 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6DN | NP166DN | np16 6dn | np166dn | Monmouthshire | Sir Fynwy | Tintern STW | 4321 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 351915 | 196412 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6DY | NP166DY | np16 6dy | np166dy | Monmouthshire | Sir Fynwy | Tintern STW | 4506 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 351686 | 196307 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6DZ | NP166DZ | np16 6dz | np166dz | Monmouthshire | Sir Fynwy | Tintern STW | 4190 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 351817 | 196595 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6EA | NP166EA | np16 6ea | np166ea | Monmouthshire | Sir Fynwy | Tintern STW | 4174 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 351458 | 196791 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6EB | NP166EB | np16 6eb | np166eb | Monmouthshire | Sir Fynwy | Tintern STW | 4379 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 351595 | 196489 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6ED | NP166ED | np16 6ed | np166ed | Monmouthshire | Sir Fynwy | Tintern STW | 4232 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 351578 | 196661 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6EE | NP166EE | np16 6ee | np166ee | Monmouthshire | Sir Fynwy | Tintern STW | 4206 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 351843 | 196566 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6EF | NP166EF | np16 6ef | np166ef | Monmouthshire | Sir Fynwy | Tintern STW | 4086 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 351565 | 196833 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6EJ | NP166EJ | np16 6ej | np166ej | Monmouthshire | Sir Fynwy | Tintern STW | 4238 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 351789 | 196555 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6EL | NP166EL | np16 6el | np166el | Monmouthshire | Sir Fynwy | Tintern STW | 4423 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 351762 | 196365 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6EN | NP166EN | np16 6en | np166en | Monmouthshire | Sir Fynwy | Tintern STW | 4302 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 351812 | 196475 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6EP | NP166EP | np16 6ep | np166ep | Monmouthshire | Sir Fynwy | Tintern STW | 4271 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 351772 | 196526 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6ER | NP166ER | np16 6er | np166er | Monmouthshire | Sir Fynwy | Tintern STW | 4259 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 351756 | 196546 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6ES | NP166ES | np16 6es | np166es | Monmouthshire | Sir Fynwy | Tintern STW | 4237 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 351773 | 196563 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6ET | NP166ET | np16 6et | np166et | Monmouthshire | Sir Fynwy | Tintern STW | 4378 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 351718 | 196433 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6EU | NP166EU | np16 6eu | np166eu | Monmouthshire | Sir Fynwy | Devauden STW | 4055 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 350645 | 196615 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6EW | NP166EW | np16 6ew | np166ew | Monmouthshire | Sir Fynwy | Tintern STW | 4296 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 351797 | 196488 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6EY | NP166EY | np16 6ey | np166ey | Monmouthshire | Sir Fynwy | Tintern STW | 4034 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 351645 | 196849 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6EZ | NP166EZ | np16 6ez | np166ez | Monmouthshire | Sir Fynwy | Tintern STW | 3781 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 351333 | 197333 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6FD | NP166FD | np16 6fd | np166fd | Monmouthshire | Sir Fynwy | Llanishen STW | 2083 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 348602 | 201238 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6HA | NP166HA | np16 6ha | np166ha | Monmouthshire | Sir Fynwy | Tintern STW | 3860 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 351541 | 197106 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6HB | NP166HB | np16 6hb | np166hb | Monmouthshire | Sir Fynwy | Tintern STW | 3886 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 351561 | 197064 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6HD | NP166HD | np16 6hd | np166hd | Monmouthshire | Sir Fynwy | Tintern STW | 3226 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 352864 | 197269 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6HE | NP166HE | np16 6he | np166he | Monmouthshire | Sir Fynwy | Tintern STW | 3933 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 352059 | 196772 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6HF | NP166HF | np16 6hf | np166hf | Monmouthshire | Sir Fynwy | Tintern STW | 2874 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 353414 | 197558 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6HG | NP166HG | np16 6hg | np166hg | Monmouthshire | Sir Fynwy | Tintern STW | 2571 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 352374 | 198120 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6HH | NP166HH | np16 6hh | np166hh | Monmouthshire | Sir Fynwy | Tintern STW | 2728 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 351928 | 198202 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6HJ | NP166HJ | np16 6hj | np166hj | Monmouthshire | Sir Fynwy | Tintern STW | 3224 | 1082 | 900to1200 | 2.17 | 1.58 | 1.16 | 20.17 | 10.76 | 11.89 | 350602 | 199020 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6HL | NP166HL | np16 6hl | np166hl | Monmouthshire | Sir Fynwy | Devauden STW | 3220 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 350484 | 199034 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6HQ | NP166HQ | np16 6hq | np166hq | Monmouthshire | Sir Fynwy | Tintern STW | 2350 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 351333 | 199524 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6HU | NP166HU | np16 6hu | np166hu | Monmouthshire | Sir Fynwy | Tintern STW | 4308 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 351715 | 196511 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NA | NP166NA | np16 6na | np166na | Monmouthshire | Sir Fynwy | WwTW | 929 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 351143 | 202958 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6ND | NP166ND | np16 6nd | np166nd | Monmouthshire | Sir Fynwy | WwTW | 330 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 350466 | 203005 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NE | NP166NE | np16 6ne | np166ne | Monmouthshire | Sir Fynwy | WwTW | 302 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 350397 | 203025 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NF | NP166NF | np16 6nf | np166nf | Monmouthshire | Sir Fynwy | WwTW | 578 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 350785 | 202603 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NG | NP166NG | np16 6ng | np166ng | Monmouthshire | Sir Fynwy | WwTW | 734 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 350804 | 203233 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NH | NP166NH | np16 6nh | np166nh | Monmouthshire | Sir Fynwy | WwTW | 916 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 351139 | 202902 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NJ | NP166NJ | np16 6nj | np166nj | Monmouthshire | Sir Fynwy | WwTW | 1994 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 352121 | 202134 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NP | NP166NP | np16 6np | np166np | Monmouthshire | Sir Fynwy | WwTW | 1553 | 1098 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.46 | 10.91 | 12.06 | 351466 | 201828 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6NQ | NP166NQ | np16 6nq | np166nq | Monmouthshire | Sir Fynwy | WwTW | 1027 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 351259 | 202728 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PE | NP166PE | np16 6pe | np166pe | Monmouthshire | Sir Fynwy | Devauden STW | 1272 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 348541 | 198903 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PF | NP166PF | np16 6pf | np166pf | Monmouthshire | Sir Fynwy | Devauden STW | 1616 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 348870 | 199082 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PH | NP166PH | np16 6ph | np166ph | Monmouthshire | Sir Fynwy | Devauden STW | 2117 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 349386 | 198870 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PS | NP166PS | np16 6ps | np166ps | Monmouthshire | Sir Fynwy | Devauden STW | 2413 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 349519 | 199733 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6PY | NP166PY | np16 6py | np166py | Monmouthshire | Sir Fynwy | WwTW | 299 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 350351 | 203047 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QH | NP166QH | np16 6qh | np166qh | Monmouthshire | Sir Fynwy | Llanishen STW | 215 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 347816 | 203227 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QN | NP166QN | np16 6qn | np166qn | Monmouthshire | Sir Fynwy | WwTW | 1325 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 349290 | 201842 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QQ | NP166QQ | np16 6qq | np166qq | Monmouthshire | Sir Fynwy | Llanishen STW | 1073 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 348540 | 203688 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QR | NP166QR | np16 6qr | np166qr | Monmouthshire | Sir Fynwy | WwTW | 1527 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 349138 | 201709 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6QW | NP166QW | np16 6qw | np166qw | Monmouthshire | Sir Fynwy | WwTW | 1382 | 1057 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.7 | 10.51 | 11.61 | 350289 | 201392 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SD | NP166SD | np16 6sd | np166sd | Monmouthshire | Sir Fynwy | Tintern STW | 563 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 353062 | 200076 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SE | NP166SE | np16 6se | np166se | Monmouthshire | Sir Fynwy | Tintern STW | 619 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 352899 | 200282 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SF | NP166SF | np16 6sf | np166sf | Monmouthshire | Sir Fynwy | Tintern STW | 582 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 353126 | 199985 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SG | NP166SG | np16 6sg | np166sg | Monmouthshire | Sir Fynwy | Tintern STW | 698 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 352885 | 200759 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SH | NP166SH | np16 6sh | np166sh | Monmouthshire | Sir Fynwy | Tintern STW | 475 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 353380 | 199971 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SJ | NP166SJ | np16 6sj | np166sj | Monmouthshire | Sir Fynwy | Tintern STW | 540 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 353084 | 200774 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SN | NP166SN | np16 6sn | np166sn | Monmouthshire | Sir Fynwy | Tintern STW | 1307 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 352734 | 201488 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SP | NP166SP | np16 6sp | np166sp | Monmouthshire | Sir Fynwy | Tintern STW | 1184 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 352775 | 201366 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SQ | NP166SQ | np16 6sq | np166sq | Monmouthshire | Sir Fynwy | Tintern STW | 540 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 353103 | 200796 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SS | NP166SS | np16 6ss | np166ss | Monmouthshire | Sir Fynwy | Devauden STW | 1331 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 348601 | 198863 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6ST | NP166ST | np16 6st | np166st | Monmouthshire | Sir Fynwy | Tintern STW | 1136 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 352603 | 201126 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SU | NP166SU | np16 6su | np166su | Monmouthshire | Sir Fynwy | Tintern STW | 1146 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 352365 | 200586 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SX | NP166SX | np16 6sx | np166sx | Monmouthshire | Sir Fynwy | Tintern STW | 773 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 352739 | 200298 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SY | NP166SY | np16 6sy | np166sy | Monmouthshire | Sir Fynwy | Tintern STW | 503 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 353066 | 200176 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6SZ | NP166SZ | np16 6sz | np166sz | Monmouthshire | Sir Fynwy | Tintern STW | 506 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 353051 | 200198 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TB | NP166TB | np16 6tb | np166tb | Monmouthshire | Sir Fynwy | Tintern STW | 446 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 353125 | 200188 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TD | NP166TD | np16 6td | np166td | Monmouthshire | Sir Fynwy | Tintern STW | 987 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 352695 | 199860 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TE | NP166TE | np16 6te | np166te | Monmouthshire | Sir Fynwy | Tintern STW | 413 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 353246 | 200105 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TF | NP166TF | np16 6tf | np166tf | Monmouthshire | Sir Fynwy | Tintern STW | 757 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 352836 | 200068 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TG | NP166TG | np16 6tg | np166tg | Monmouthshire | Sir Fynwy | Tintern STW | 1073 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 352659 | 199765 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TH | NP166TH | np16 6th | np166th | Monmouthshire | Sir Fynwy | Tintern STW | 1172 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 352352 | 200194 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TJ | NP166TJ | np16 6tj | np166tj | Monmouthshire | Sir Fynwy | Tintern STW | 1034 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 352493 | 200199 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TL | NP166TL | np16 6tl | np166tl | Monmouthshire | Sir Fynwy | Tintern STW | 1178 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 352341 | 200224 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TN | NP166TN | np16 6tn | np166tn | Monmouthshire | Sir Fynwy | Tintern STW | 1290 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 352228 | 200221 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TP | NP166TP | np16 6tp | np166tp | Monmouthshire | Sir Fynwy | WwTW | 2627 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 350775 | 200203 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TQ | NP166TQ | np16 6tq | np166tq | Monmouthshire | Sir Fynwy | Tintern STW | 843 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 352709 | 200139 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TR | NP166TR | np16 6tr | np166tr | Monmouthshire | Sir Fynwy | Tintern STW | 2326 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 351175 | 200415 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TS | NP166TS | np16 6ts | np166ts | Monmouthshire | Sir Fynwy | Tintern STW | 2177 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 351333 | 200235 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TT | NP166TT | np16 6tt | np166tt | Monmouthshire | Sir Fynwy | WwTW | 2569 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 350807 | 200269 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TU | NP166TU | np16 6tu | np166tu | Monmouthshire | Sir Fynwy | Tintern STW | 1922 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 351585 | 200277 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TW | NP166TW | np16 6tw | np166tw | Monmouthshire | Sir Fynwy | Tintern STW | 1317 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 352194 | 200265 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TX | NP166TX | np16 6tx | np166tx | Monmouthshire | Sir Fynwy | Tintern STW | 1038 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 352794 | 201190 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6TY | NP166TY | np16 6ty | np166ty | Monmouthshire | Sir Fynwy | Tintern STW | 890 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 352833 | 201018 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6UG | NP166UG | np16 6ug | np166ug | Monmouthshire | Sir Fynwy | WwTW | 927 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 351160 | 202770 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6UJ | NP166UJ | np16 6uj | np166uj | Monmouthshire | Sir Fynwy | Tintern STW | 707 | 1054 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.64 | 10.48 | 11.58 | 352857 | 200137 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6UL | NP166UL | np16 6ul | np166ul | Monmouthshire | Sir Fynwy | WwTW | 1259 | 1108 | 900to1200 | 2.22 | 1.62 | 1.19 | 20.65 | 11.01 | 12.17 | 351491 | 202760 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6UN | NP166UN | np16 6un | np166un | Monmouthshire | Sir Fynwy | Tintern STW | 9127 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 353705 | 191309 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6UP | NP166UP | np16 6up | np166up | Monmouthshire | Sir Fynwy | Tintern STW | 9453 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 353587 | 190981 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 6ZD | NP166ZD | np16 6zd | np166zd | Monmouthshire | Sir Fynwy | Tintern STW | 6670 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353529 | 193763 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 7NX | NP167NX | np16 7nx | np167nx | Monmouthshire | Sir Fynwy | Tintern STW | 522 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 353545 | 200950 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 7WP | NP167WP | np16 7wp | np167wp | Monmouthshire | Sir Fynwy | Tintern STW | 6670 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353529 | 193763 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 7WZ | NP167WZ | np16 7wz | np167wz | Monmouthshire | Sir Fynwy | Tintern STW | 6670 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353529 | 193763 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 9AX | NP169AX | np16 9ax | np169ax | Monmouthshire | Sir Fynwy | Tintern STW | 6670 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353529 | 193763 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 9BQ | NP169BQ | np16 9bq | np169bq | Monmouthshire | Sir Fynwy | Tintern STW | 6670 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353529 | 193763 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 9DA | NP169DA | np16 9da | np169da | Monmouthshire | Sir Fynwy | Tintern STW | 6670 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353529 | 193763 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 9DD | NP169DD | np16 9dd | np169dd | Monmouthshire | Sir Fynwy | Tintern STW | 6670 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353529 | 193763 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP16 9DE | NP169DE | np16 9de | np169de | Monmouthshire | Sir Fynwy | Tintern STW | 6670 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 353529 | 193763 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3AB | NP253AB | np25 3ab | np253ab | Monmouthshire | Sir Fynwy | Rockfield STW | 2383 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350914 | 214487 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3AE | NP253AE | np25 3ae | np253ae | Monmouthshire | Sir Fynwy | Monmouth STW | 1354 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351007 | 213043 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3AR | NP253AR | np25 3ar | np253ar | Monmouthshire | Sir Fynwy | Rockfield STW | 1788 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350242 | 214205 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3AS | NP253AS | np25 3as | np253as | Monmouthshire | Sir Fynwy | Rockfield STW | 1791 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350221 | 214136 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3AT | NP253AT | np25 3at | np253at | Monmouthshire | Sir Fynwy | Rockfield STW | 1852 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350273 | 214102 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3AU | NP253AU | np25 3au | np253au | Monmouthshire | Sir Fynwy | Rockfield STW | 1801 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350217 | 214099 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3AX | NP253AX | np25 3ax | np253ax | Monmouthshire | Sir Fynwy | Monmouth STW | 1891 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350726 | 213505 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3AY | NP253AY | np25 3ay | np253ay | Monmouthshire | Sir Fynwy | Rockfield STW | 2105 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350388 | 213755 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3AZ | NP253AZ | np25 3az | np253az | Monmouthshire | Sir Fynwy | Rockfield STW | 2044 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350337 | 213789 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3BD | NP253BD | np25 3bd | np253bd | Monmouthshire | Sir Fynwy | Rockfield STW | 1903 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 350438 | 214550 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3BE | NP253BE | np25 3be | np253be | Monmouthshire | Sir Fynwy | Rockfield STW | 1856 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350376 | 214449 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3BG | NP253BG | np25 3bg | np253bg | Monmouthshire | Sir Fynwy | Rockfield STW | 2045 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 350579 | 214528 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3BQ | NP253BQ | np25 3bq | np253bq | Monmouthshire | Sir Fynwy | Monmouth STW | 1254 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350841 | 212841 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3BR | NP253BR | np25 3br | np253br | Monmouthshire | Sir Fynwy | Monmouth STW | 1372 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350796 | 212952 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3BS | NP253BS | np25 3bs | np253bs | Monmouthshire | Sir Fynwy | Monmouth STW | 1392 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350709 | 212917 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3BT | NP253BT | np25 3bt | np253bt | Monmouthshire | Sir Fynwy | Monmouth STW | 1312 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350798 | 212882 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3BU | NP253BU | np25 3bu | np253bu | Monmouthshire | Sir Fynwy | Monmouth STW | 1334 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350830 | 212929 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3BW | NP253BW | np25 3bw | np253bw | Monmouthshire | Sir Fynwy | Monmouth STW | 1251 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351019 | 212936 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3BX | NP253BX | np25 3bx | np253bx | Monmouthshire | Sir Fynwy | Monmouth STW | 1315 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350831 | 212907 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3BY | NP253BY | np25 3by | np253by | Monmouthshire | Sir Fynwy | Monmouth STW | 1300 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350969 | 212966 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3BZ | NP253BZ | np25 3bz | np253bz | Monmouthshire | Sir Fynwy | Monmouth STW | 1288 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350927 | 212931 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DA | NP253DA | np25 3da | np253da | Monmouthshire | Sir Fynwy | Monmouth STW | 1288 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350966 | 212951 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DB | NP253DB | np25 3db | np253db | Monmouthshire | Sir Fynwy | Monmouth STW | 1261 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350905 | 212889 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DD | NP253DD | np25 3dd | np253dd | Monmouthshire | Sir Fynwy | Monmouth STW | 1197 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350959 | 212845 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DE | NP253DE | np25 3de | np253de | Monmouthshire | Sir Fynwy | Monmouth STW | 1159 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350974 | 212810 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DF | NP253DF | np25 3df | np253df | Monmouthshire | Sir Fynwy | Monmouth STW | 1183 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350942 | 212820 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DG | NP253DG | np25 3dg | np253dg | Monmouthshire | Sir Fynwy | Monmouth STW | 1168 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350863 | 212752 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DH | NP253DH | np25 3dh | np253dh | Monmouthshire | Sir Fynwy | Monmouth STW | 1078 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350931 | 212689 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DJ | NP253DJ | np25 3dj | np253dj | Monmouthshire | Sir Fynwy | Monmouth STW | 1284 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351105 | 213005 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DL | NP253DL | np25 3dl | np253dl | Monmouthshire | Sir Fynwy | Monmouth STW | 1185 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351067 | 212884 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DN | NP253DN | np25 3dn | np253dn | Monmouthshire | Sir Fynwy | Monmouth STW | 1262 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351085 | 212975 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DP | NP253DP | np25 3dp | np253dp | Monmouthshire | Sir Fynwy | Monmouth STW | 1276 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351165 | 213017 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DQ | NP253DQ | np25 3dq | np253dq | Monmouthshire | Sir Fynwy | Rockfield STW | 2123 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350647 | 214453 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DR | NP253DR | np25 3dr | np253dr | Monmouthshire | Sir Fynwy | Monmouth STW | 1220 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351143 | 212951 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DS | NP253DS | np25 3ds | np253ds | Monmouthshire | Sir Fynwy | Monmouth STW | 1171 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351134 | 212896 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DT | NP253DT | np25 3dt | np253dt | Monmouthshire | Sir Fynwy | Monmouth STW | 1305 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350993 | 212983 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DU | NP253DU | np25 3du | np253du | Monmouthshire | Sir Fynwy | Rockfield STW | 2226 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350754 | 214475 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DX | NP253DX | np25 3dx | np253dx | Monmouthshire | Sir Fynwy | Monmouth STW | 1337 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350763 | 212888 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DY | NP253DY | np25 3dy | np253dy | Monmouthshire | Sir Fynwy | Monmouth STW | 1316 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350752 | 212854 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3DZ | NP253DZ | np25 3dz | np253dz | Monmouthshire | Sir Fynwy | Monmouth STW | 1236 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350802 | 212792 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3EA | NP253EA | np25 3ea | np253ea | Monmouthshire | Sir Fynwy | Monmouth STW | 1232 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350769 | 212762 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3EB | NP253EB | np25 3eb | np253eb | Monmouthshire | Sir Fynwy | Monmouth STW | 1342 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350576 | 212736 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3ED | NP253ED | np25 3ed | np253ed | Monmouthshire | Sir Fynwy | Monmouth STW | 1224 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350629 | 212621 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3EE | NP253EE | np25 3ee | np253ee | Monmouthshire | Sir Fynwy | Monmouth STW | 1280 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350717 | 212781 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3EF | NP253EF | np25 3ef | np253ef | Monmouthshire | Sir Fynwy | Monmouth STW | 1308 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350680 | 212787 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3EG | NP253EG | np25 3eg | np253eg | Monmouthshire | Sir Fynwy | Monmouth STW | 1300 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350489 | 212571 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3EH | NP253EH | np25 3eh | np253eh | Monmouthshire | Sir Fynwy | Monmouth STW | 1363 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350627 | 212813 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3EJ | NP253EJ | np25 3ej | np253ej | Monmouthshire | Sir Fynwy | Monmouth STW | 1210 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350663 | 212636 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3EL | NP253EL | np25 3el | np253el | Monmouthshire | Sir Fynwy | Monmouth STW | 1337 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350467 | 212602 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3EN | NP253EN | np25 3en | np253en | Monmouthshire | Sir Fynwy | Monmouth STW | 1265 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350635 | 212686 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3EQ | NP253EQ | np25 3eq | np253eq | Monmouthshire | Sir Fynwy | Monmouth STW | 1276 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350553 | 212612 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3ER | NP253ER | np25 3er | np253er | Monmouthshire | Sir Fynwy | Monmouth STW | 1258 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350709 | 212746 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3EW | NP253EW | np25 3ew | np253ew | Monmouthshire | Sir Fynwy | Monmouth STW | 1304 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350567 | 212672 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3EX | NP253EX | np25 3ex | np253ex | Monmouthshire | Sir Fynwy | Monmouth STW | 1394 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350580 | 212812 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3GA | NP253GA | np25 3ga | np253ga | Monmouthshire | Sir Fynwy | Rockfield STW | 2436 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 350979 | 214606 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3GB | NP253GB | np25 3gb | np253gb | Monmouthshire | Sir Fynwy | Rockfield STW | 2466 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350993 | 214448 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3GD | NP253GD | np25 3gd | np253gd | Monmouthshire | Sir Fynwy | Rockfield STW | 2432 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350951 | 214400 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3GE | NP253GE | np25 3ge | np253ge | Monmouthshire | Sir Fynwy | Rockfield STW | 2393 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 350935 | 214597 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3GZ | NP253GZ | np25 3gz | np253gz | Monmouthshire | Sir Fynwy | Monmouth STW | 303 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351604 | 212089 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HA | NP253HA | np25 3ha | np253ha | Monmouthshire | Sir Fynwy | Monmouth STW | 716 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351473 | 212508 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HB | NP253HB | np25 3hb | np253hb | Monmouthshire | Sir Fynwy | Monmouth STW | 2236 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350954 | 213954 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HD | NP253HD | np25 3hd | np253hd | Monmouthshire | Sir Fynwy | Rockfield STW | 2361 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350888 | 214460 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HE | NP253HE | np25 3he | np253he | Monmouthshire | Sir Fynwy | Monmouth STW | 1643 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351197 | 213403 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HF | NP253HF | np25 3hf | np253hf | Monmouthshire | Sir Fynwy | Monmouth STW | 1678 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351102 | 213416 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HG | NP253HG | np25 3hg | np253hg | Monmouthshire | Sir Fynwy | Monmouth STW | 1817 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350946 | 213514 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HH | NP253HH | np25 3hh | np253hh | Monmouthshire | Sir Fynwy | Monmouth STW | 2393 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350991 | 214125 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HJ | NP253HJ | np25 3hj | np253hj | Monmouthshire | Sir Fynwy | Monmouth STW | 2067 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 351022 | 213797 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HL | NP253HL | np25 3hl | np253hl | Monmouthshire | Sir Fynwy | Monmouth STW | 2291 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 351044 | 214033 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HN | NP253HN | np25 3hn | np253hn | Monmouthshire | Sir Fynwy | Monmouth STW | 2335 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 351072 | 214083 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HP | NP253HP | np25 3hp | np253hp | Monmouthshire | Sir Fynwy | Rockfield STW | 2407 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350880 | 214180 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HQ | NP253HQ | np25 3hq | np253hq | Monmouthshire | Sir Fynwy | Monmouth STW | 2101 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350966 | 213817 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HR | NP253HR | np25 3hr | np253hr | Monmouthshire | Sir Fynwy | Rockfield STW | 2192 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350700 | 214356 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HS | NP253HS | np25 3hs | np253hs | Monmouthshire | Sir Fynwy | Rockfield STW | 2083 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350511 | 214079 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HT | NP253HT | np25 3ht | np253ht | Monmouthshire | Sir Fynwy | Rockfield STW | 2045 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350515 | 214217 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HU | NP253HU | np25 3hu | np253hu | Monmouthshire | Sir Fynwy | Rockfield STW | 1969 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350455 | 214285 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HW | NP253HW | np25 3hw | np253hw | Monmouthshire | Sir Fynwy | Monmouth STW | 2328 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350816 | 214009 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HX | NP253HX | np25 3hx | np253hx | Monmouthshire | Sir Fynwy | Rockfield STW | 1881 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350385 | 214370 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HY | NP253HY | np25 3hy | np253hy | Monmouthshire | Sir Fynwy | Rockfield STW | 1947 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350360 | 214065 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3HZ | NP253HZ | np25 3hz | np253hz | Monmouthshire | Sir Fynwy | Rockfield STW | 1986 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350386 | 214025 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JD | NP253JD | np25 3jd | np253jd | Monmouthshire | Sir Fynwy | Rockfield STW | 2082 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350581 | 214325 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JE | NP253JE | np25 3je | np253je | Monmouthshire | Sir Fynwy | Rockfield STW | 1916 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350325 | 214060 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JG | NP253JG | np25 3jg | np253jg | Monmouthshire | Sir Fynwy | Rockfield STW | 2140 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 350676 | 214542 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JH | NP253JH | np25 3jh | np253jh | Monmouthshire | Sir Fynwy | Monmouth STW | 747 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 352243 | 212022 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JJ | NP253JJ | np25 3jj | np253jj | Monmouthshire | Sir Fynwy | Rockfield STW | 2401 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350920 | 214398 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JL | NP253JL | np25 3jl | np253jl | Monmouthshire | Sir Fynwy | Rockfield STW | 2147 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350616 | 214199 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JN | NP253JN | np25 3jn | np253jn | Monmouthshire | Sir Fynwy | Monmouth STW | 511 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351997 | 212006 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JP | NP253JP | np25 3jp | np253jp | Monmouthshire | Sir Fynwy | Monmouth STW | 612 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 351471 | 212404 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JQ | NP253JQ | np25 3jq | np253jq | Monmouthshire | Sir Fynwy | Monmouth STW | 655 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 352061 | 212181 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JR | NP253JR | np25 3jr | np253jr | Monmouthshire | Sir Fynwy | Monmouth STW | 564 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351866 | 212249 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JS | NP253JS | np25 3js | np253js | Monmouthshire | Sir Fynwy | Monmouth STW | 678 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 352115 | 212141 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JU | NP253JU | np25 3ju | np253ju | Monmouthshire | Sir Fynwy | Monmouth STW | 850 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 352309 | 212138 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JW | NP253JW | np25 3jw | np253jw | Monmouthshire | Sir Fynwy | Monmouth STW | 533 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351984 | 212077 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JX | NP253JX | np25 3jx | np253jx | Monmouthshire | Sir Fynwy | Monmouth STW | 510 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 351452 | 212299 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JY | NP253JY | np25 3jy | np253jy | Monmouthshire | Sir Fynwy | Monmouth STW | 581 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351720 | 212345 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3JZ | NP253JZ | np25 3jz | np253jz | Monmouthshire | Sir Fynwy | Monmouth STW | 562 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351734 | 212319 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LA | NP253LA | np25 3la | np253la | Monmouthshire | Sir Fynwy | Monmouth STW | 665 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351785 | 212410 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LB | NP253LB | np25 3lb | np253lb | Monmouthshire | Sir Fynwy | Monmouth STW | 646 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351907 | 212321 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LD | NP253LD | np25 3ld | np253ld | Monmouthshire | Sir Fynwy | Monmouth STW | 467 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351885 | 212101 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LE | NP253LE | np25 3le | np253le | Monmouthshire | Sir Fynwy | Monmouth STW | 727 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 352050 | 212305 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LF | NP253LF | np25 3lf | np253lf | Monmouthshire | Sir Fynwy | Monmouth STW | 653 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351991 | 212259 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LG | NP253LG | np25 3lg | np253lg | Monmouthshire | Sir Fynwy | Monmouth STW | 783 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 352006 | 212418 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LH | NP253LH | np25 3lh | np253lh | Monmouthshire | Sir Fynwy | Monmouth STW | 733 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351552 | 212527 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LJ | NP253LJ | np25 3lj | np253lj | Monmouthshire | Sir Fynwy | Monmouth STW | 715 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351605 | 212506 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LL | NP253LL | np25 3ll | np253ll | Monmouthshire | Sir Fynwy | Monmouth STW | 439 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351932 | 211975 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LN | NP253LN | np25 3ln | np253ln | Monmouthshire | Sir Fynwy | Monmouth STW | 847 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351691 | 212627 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LP | NP253LP | np25 3lp | np253lp | Monmouthshire | Sir Fynwy | Monmouth STW | 863 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351618 | 212653 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LQ | NP253LQ | np25 3lq | np253lq | Monmouthshire | Sir Fynwy | Monmouth STW | 907 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351688 | 212688 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LR | NP253LR | np25 3lr | np253lr | Monmouthshire | Sir Fynwy | Monmouth STW | 1355 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350980 | 213032 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LS | NP253LS | np25 3ls | np253ls | Monmouthshire | Sir Fynwy | Monmouth STW | 1002 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351261 | 212759 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LT | NP253LT | np25 3lt | np253lt | Monmouthshire | Sir Fynwy | Monmouth STW | 1095 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351377 | 212879 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LU | NP253LU | np25 3lu | np253lu | Monmouthshire | Sir Fynwy | Monmouth STW | 615 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 352016 | 212174 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LW | NP253LW | np25 3lw | np253lw | Monmouthshire | Sir Fynwy | Monmouth STW | 1397 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350984 | 213079 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LX | NP253LX | np25 3lx | np253lx | Monmouthshire | Sir Fynwy | Monmouth STW | 854 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351418 | 212641 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LY | NP253LY | np25 3ly | np253ly | Monmouthshire | Sir Fynwy | Monmouth STW | 709 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 351393 | 212490 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3LZ | NP253LZ | np25 3lz | np253lz | Monmouthshire | Sir Fynwy | Monmouth STW | 374 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 351402 | 212145 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NA | NP253NA | np25 3na | np253na | Monmouthshire | Sir Fynwy | Monmouth STW | 652 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 351379 | 212429 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NB | NP253NB | np25 3nb | np253nb | Monmouthshire | Sir Fynwy | Monmouth STW | 328 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351518 | 212123 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3ND | NP253ND | np25 3nd | np253nd | Monmouthshire | Sir Fynwy | Monmouth STW | 509 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351793 | 212232 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NE | NP253NE | np25 3ne | np253ne | Monmouthshire | Sir Fynwy | Monmouth STW | 387 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351612 | 212173 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NF | NP253NF | np25 3nf | np253nf | Monmouthshire | Sir Fynwy | Monmouth STW | 467 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351699 | 212231 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NG | NP253NG | np25 3ng | np253ng | Monmouthshire | Sir Fynwy | Monmouth STW | 924 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351543 | 212719 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NH | NP253NH | np25 3nh | np253nh | Monmouthshire | Sir Fynwy | Monmouth STW | 2969 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 352830 | 214464 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NJ | NP253NJ | np25 3nj | np253nj | Monmouthshire | Sir Fynwy | Monmouth STW | 3196 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353014 | 214625 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NL | NP253NL | np25 3nl | np253nl | Monmouthshire | Sir Fynwy | Monmouth STW | 3981 | 877 | 700to900 | 1.76 | 1.28 | 0.94 | 16.35 | 8.72 | 9.64 | 353423 | 215296 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NN | NP253NN | np25 3nn | np253nn | Monmouthshire | Sir Fynwy | Monmouth STW | 332 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351708 | 212076 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NP | NP253NP | np25 3np | np253np | Monmouthshire | Sir Fynwy | Monmouth STW | 559 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351635 | 212344 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NQ | NP253NQ | np25 3nq | np253nq | Monmouthshire | Sir Fynwy | Monmouth STW | 1424 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351904 | 213169 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NR | NP253NR | np25 3nr | np253nr | Monmouthshire | Sir Fynwy | Rockfield STW | 2174 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350576 | 213993 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NS | NP253NS | np25 3ns | np253ns | Monmouthshire | Sir Fynwy | Rockfield STW | 2105 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350504 | 213998 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NT | NP253NT | np25 3nt | np253nt | Monmouthshire | Sir Fynwy | Monmouth STW | 2163 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350662 | 213774 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NU | NP253NU | np25 3nu | np253nu | Monmouthshire | Sir Fynwy | Monmouth STW | 2279 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350663 | 213901 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NW | NP253NW | np25 3nw | np253nw | Monmouthshire | Sir Fynwy | Rockfield STW | 2298 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350690 | 213946 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NX | NP253NX | np25 3nx | np253nx | Monmouthshire | Sir Fynwy | Monmouth STW | 1425 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350913 | 213078 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NY | NP253NY | np25 3ny | np253ny | Monmouthshire | Sir Fynwy | Monmouth STW | 1345 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350808 | 212928 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3NZ | NP253NZ | np25 3nz | np253nz | Monmouthshire | Sir Fynwy | Monmouth STW | 1454 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350929 | 213118 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PA | NP253PA | np25 3pa | np253pa | Monmouthshire | Sir Fynwy | Monmouth STW | 1526 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350972 | 213214 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PB | NP253PB | np25 3pb | np253pb | Monmouthshire | Sir Fynwy | Monmouth STW | 1669 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350951 | 213359 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PD | NP253PD | np25 3pd | np253pd | Monmouthshire | Sir Fynwy | Monmouth STW | 1651 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350922 | 213329 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PE | NP253PE | np25 3pe | np253pe | Monmouthshire | Sir Fynwy | Monmouth STW | 1750 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350917 | 213433 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PF | NP253PF | np25 3pf | np253pf | Monmouthshire | Sir Fynwy | Monmouth STW | 1574 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351018 | 213282 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PG | NP253PG | np25 3pg | np253pg | Monmouthshire | Sir Fynwy | Monmouth STW | 1536 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351118 | 213274 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PH | NP253PH | np25 3ph | np253ph | Monmouthshire | Sir Fynwy | Monmouth STW | 1498 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351077 | 213222 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PJ | NP253PJ | np25 3pj | np253pj | Monmouthshire | Sir Fynwy | Monmouth STW | 1749 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 351294 | 213527 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PL | NP253PL | np25 3pl | np253pl | Monmouthshire | Sir Fynwy | Monmouth STW | 1453 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351062 | 213169 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PN | NP253PN | np25 3pn | np253pn | Monmouthshire | Sir Fynwy | Monmouth STW | 422 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351507 | 212216 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PP | NP253PP | np25 3pp | np253pp | Monmouthshire | Sir Fynwy | Monmouth STW | 1649 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351469 | 213442 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PQ | NP253PQ | np25 3pq | np253pq | Monmouthshire | Sir Fynwy | Monmouth STW | 1707 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351294 | 213485 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PR | NP253PR | np25 3pr | np253pr | Monmouthshire | Sir Fynwy | Monmouth STW | 1630 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351306 | 213409 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PS | NP253PS | np25 3ps | np253ps | Monmouthshire | Sir Fynwy | Monmouth STW | 1328 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350536 | 212672 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PT | NP253PT | np25 3pt | np253pt | Monmouthshire | Sir Fynwy | Monmouth STW | 1368 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350465 | 212650 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PU | NP253PU | np25 3pu | np253pu | Monmouthshire | Sir Fynwy | Monmouth STW | 2154 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350854 | 213839 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PW | NP253PW | np25 3pw | np253pw | Monmouthshire | Sir Fynwy | Monmouth STW | 709 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351650 | 212494 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PX | NP253PX | np25 3px | np253px | Monmouthshire | Sir Fynwy | Monmouth STW | 1398 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351036 | 213102 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3PY | NP253PY | np25 3py | np253py | Monmouthshire | Sir Fynwy | Monmouth STW | 1781 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350881 | 213452 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3QG | NP253QG | np25 3qg | np253qg | Monmouthshire | Sir Fynwy | Monmouth STW | 1184 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351563 | 212978 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SA | NP253SA | np25 3sa | np253sa | Monmouthshire | Sir Fynwy | Monmouth STW | 1262 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351911 | 212998 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SB | NP253SB | np25 3sb | np253sb | Monmouthshire | Sir Fynwy | Monmouth STW | 2281 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 352698 | 213755 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SD | NP253SD | np25 3sd | np253sd | Monmouthshire | Sir Fynwy | Monmouth STW | 1214 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 352469 | 212566 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SE | NP253SE | np25 3se | np253se | Monmouthshire | Sir Fynwy | Monmouth STW | 1325 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 352550 | 212642 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SF | NP253SF | np25 3sf | np253sf | Monmouthshire | Sir Fynwy | Monmouth STW | 1414 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 352685 | 212613 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SG | NP253SG | np25 3sg | np253sg | Monmouthshire | Sir Fynwy | Monmouth STW | 1475 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351436 | 213266 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SH | NP253SH | np25 3sh | np253sh | Monmouthshire | Sir Fynwy | Monmouth STW | 1496 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351468 | 213289 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SJ | NP253SJ | np25 3sj | np253sj | Monmouthshire | Sir Fynwy | Monmouth STW | 1863 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 351791 | 213639 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SN | NP253SN | np25 3sn | np253sn | Monmouthshire | Sir Fynwy | Monmouth STW | 2313 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 351737 | 214098 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SP | NP253SP | np25 3sp | np253sp | Monmouthshire | Sir Fynwy | Monmouth STW | 2735 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 352178 | 214452 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SQ | NP253SQ | np25 3sq | np253sq | Monmouthshire | Sir Fynwy | Monmouth STW | 1464 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351426 | 213255 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SW | NP253SW | np25 3sw | np253sw | Monmouthshire | Sir Fynwy | Monmouth STW | 2058 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 352021 | 213793 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SY | NP253SY | np25 3sy | np253sy | Monmouthshire | Sir Fynwy | Monmouth STW | 1871 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 351934 | 213622 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3SZ | NP253SZ | np25 3sz | np253sz | Monmouthshire | Sir Fynwy | Rockfield STW | 2185 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 350652 | 214187 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3TB | NP253TB | np25 3tb | np253tb | Monmouthshire | Sir Fynwy | Monmouth STW | 773 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351871 | 212489 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3TD | NP253TD | np25 3td | np253td | Monmouthshire | Sir Fynwy | Monmouth STW | 863 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351801 | 212615 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3TE | NP253TE | np25 3te | np253te | Monmouthshire | Sir Fynwy | Monmouth STW | 785 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351801 | 212532 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3TF | NP253TF | np25 3tf | np253tf | Monmouthshire | Sir Fynwy | Monmouth STW | 817 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351821 | 212559 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3TG | NP253TG | np25 3tg | np253tg | Monmouthshire | Sir Fynwy | Monmouth STW | 935 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351795 | 212692 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3TH | NP253TH | np25 3th | np253th | Monmouthshire | Sir Fynwy | Monmouth STW | 823 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351898 | 212532 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3TJ | NP253TJ | np25 3tj | np253tj | Monmouthshire | Sir Fynwy | Monmouth STW | 751 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351930 | 212432 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3TL | NP253TL | np25 3tl | np253tl | Monmouthshire | Sir Fynwy | Monmouth STW | 703 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351880 | 212406 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3TN | NP253TN | np25 3tn | np253tn | Monmouthshire | Sir Fynwy | Monmouth STW | 968 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351803 | 212724 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3TP | NP253TP | np25 3tp | np253tp | Monmouthshire | Sir Fynwy | Monmouth STW | 693 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351746 | 212454 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3TY | NP253TY | np25 3ty | np253ty | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3UA | NP253UA | np25 3ua | np253ua | Monmouthshire | Sir Fynwy | Monmouth STW | 1265 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350811 | 212834 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3UY | NP253UY | np25 3uy | np253uy | Monmouthshire | Sir Fynwy | Monmouth STW | 1134 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350840 | 212693 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3UZ | NP253UZ | np25 3uz | np253uz | Monmouthshire | Sir Fynwy | Monmouth STW | 1196 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350730 | 212682 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3XA | NP253XA | np25 3xa | np253xa | Monmouthshire | Sir Fynwy | Monmouth STW | 1399 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350779 | 212974 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3XE | NP253XE | np25 3xe | np253xe | Monmouthshire | Sir Fynwy | Monmouth STW | 1332 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350804 | 212910 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3XH | NP253XH | np25 3xh | np253xh | Monmouthshire | Sir Fynwy | Monmouth STW | 1284 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350703 | 212775 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3XJ | NP253XJ | np25 3xj | np253xj | Monmouthshire | Sir Fynwy | Monmouth STW | 1259 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350644 | 212687 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3XP | NP253XP | np25 3xp | np253xp | Monmouthshire | Sir Fynwy | Monmouth STW | 1062 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350994 | 212710 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3YD | NP253YD | np25 3yd | np253yd | Monmouthshire | Sir Fynwy | Monmouth STW | 1334 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 351688 | 213119 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3YR | NP253YR | np25 3yr | np253yr | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 3YT | NP253YT | np25 3yt | np253yt | Monmouthshire | Sir Fynwy | Monmouth STW | 1410 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 351196 | 213164 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AB | NP254AB | np25 4ab | np254ab | Monmouthshire | Sir Fynwy | Monmouth STW | 1048 | 923 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.2 | 9.18 | 10.14 | 350572 | 211375 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AD | NP254AD | np25 4ad | np254ad | Monmouthshire | Sir Fynwy | Trellech STW | 2354 | 1043 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.44 | 10.37 | 11.46 | 349697 | 207844 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AF | NP254AF | np25 4af | np254af | Monmouthshire | Sir Fynwy | Trellech STW | 1666 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 350216 | 207135 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AG | NP254AG | np25 4ag | np254ag | Monmouthshire | Sir Fynwy | Narth WwTW | 1071 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 351227 | 207056 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AH | NP254AH | np25 4ah | np254ah | Monmouthshire | Sir Fynwy | Narth WwTW | 2482 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 351766 | 209205 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AJ | NP254AJ | np25 4aj | np254aj | Monmouthshire | Sir Fynwy | Narth WwTW | 2521 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 353088 | 209154 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AL | NP254AL | np25 4al | np254al | Monmouthshire | Sir Fynwy | Monmouth STW | 2888 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 353584 | 209765 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AN | NP254AN | np25 4an | np254an | Monmouthshire | Sir Fynwy | Monmouth STW | 2250 | 974 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.15 | 9.68 | 10.7 | 353166 | 210249 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AP | NP254AP | np25 4ap | np254ap | Monmouthshire | Sir Fynwy | Monmouth STW | 2210 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 352111 | 209663 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AQ | NP254AQ | np25 4aq | np254aq | Monmouthshire | Sir Fynwy | Narth WwTW | 1470 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 351208 | 207800 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AR | NP254AR | np25 4ar | np254ar | Monmouthshire | Sir Fynwy | Monmouth STW | 2294 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 351799 | 209517 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AT | NP254AT | np25 4at | np254at | Monmouthshire | Sir Fynwy | Llandogo STW | 423 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352694 | 204349 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AU | NP254AU | np25 4au | np254au | Monmouthshire | Sir Fynwy | Monmouth STW | 2123 | 974 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.15 | 9.68 | 10.7 | 352774 | 210074 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AW | NP254AW | np25 4aw | np254aw | Monmouthshire | Sir Fynwy | Monmouth STW | 1542 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 352493 | 210590 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4AZ | NP254AZ | np25 4az | np254az | Monmouthshire | Sir Fynwy | Dingestow STW | 134 | 918 | 900to1200 | 1.84 | 1.34 | 0.99 | 17.11 | 9.13 | 10.09 | 345931 | 209922 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BA | NP254BA | np25 4ba | np254ba | Monmouthshire | Sir Fynwy | Rockfield STW | 1978 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350369 | 214006 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BD | NP254BD | np25 4bd | np254bd | Monmouthshire | Sir Fynwy | Monmouth STW | 2423 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 349465 | 210533 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BE | NP254BE | np25 4be | np254be | Monmouthshire | Sir Fynwy | Dingestow STW | 138 | 918 | 900to1200 | 1.84 | 1.34 | 0.99 | 17.11 | 9.13 | 10.09 | 345819 | 210168 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BG | NP254BG | np25 4bg | np254bg | Monmouthshire | Sir Fynwy | Dingestow STW | 1872 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 344550 | 208744 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BH | NP254BH | np25 4bh | np254bh | Monmouthshire | Sir Fynwy | Dingestow STW | 217 | 918 | 900to1200 | 1.84 | 1.34 | 0.99 | 17.11 | 9.13 | 10.09 | 345761 | 210224 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BJ | NP254BJ | np25 4bj | np254bj | Monmouthshire | Sir Fynwy | Dingestow STW | 532 | 918 | 900to1200 | 1.84 | 1.34 | 0.99 | 17.11 | 9.13 | 10.09 | 345914 | 209519 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BL | NP254BL | np25 4bl | np254bl | Monmouthshire | Sir Fynwy | Dingestow STW | 1683 | 874 | 700to900 | 1.75 | 1.28 | 0.94 | 16.29 | 8.69 | 9.6 | 347572 | 210096 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BP | NP254BP | np25 4bp | np254bp | Monmouthshire | Sir Fynwy | Dingestow STW | 545 | 918 | 900to1200 | 1.84 | 1.34 | 0.99 | 17.11 | 9.13 | 10.09 | 346376 | 209804 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BQ | NP254BQ | np25 4bq | np254bq | Monmouthshire | Sir Fynwy | Dingestow STW | 885 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 346087 | 209188 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BR | NP254BR | np25 4br | np254br | Monmouthshire | Sir Fynwy | Dingestow STW | 2031 | 904 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.85 | 8.99 | 9.93 | 344376 | 208698 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BS | NP254BS | np25 4bs | np254bs | Monmouthshire | Sir Fynwy | Dingestow STW | 1477 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 345589 | 208605 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BW | NP254BW | np25 4bw | np254bw | Monmouthshire | Sir Fynwy | Dingestow STW | 2576 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 345682 | 207483 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BX | NP254BX | np25 4bx | np254bx | Monmouthshire | Sir Fynwy | Dingestow STW | 867 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 346752 | 209960 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BY | NP254BY | np25 4by | np254by | Monmouthshire | Sir Fynwy | Dingestow STW | 169 | 918 | 900to1200 | 1.84 | 1.34 | 0.99 | 17.11 | 9.13 | 10.09 | 345738 | 210124 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4BZ | NP254BZ | np25 4bz | np254bz | Monmouthshire | Sir Fynwy | Dingestow STW | 180 | 918 | 900to1200 | 1.84 | 1.34 | 0.99 | 17.11 | 9.13 | 10.09 | 346005 | 209911 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DJ | NP254DJ | np25 4dj | np254dj | Monmouthshire | Sir Fynwy | Dingestow STW | 2294 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 346045 | 212338 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DL | NP254DL | np25 4dl | np254dl | Monmouthshire | Sir Fynwy | Dingestow STW | 888 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 346581 | 210607 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DN | NP254DN | np25 4dn | np254dn | Monmouthshire | Sir Fynwy | Dingestow STW | 2842 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 348584 | 210952 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DP | NP254DP | np25 4dp | np254dp | Monmouthshire | Sir Fynwy | Dingestow STW | 240 | 918 | 900to1200 | 1.84 | 1.34 | 0.99 | 17.11 | 9.13 | 10.09 | 345711 | 210209 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DQ | NP254DQ | np25 4dq | np254dq | Monmouthshire | Sir Fynwy | Monmouth STW | 2348 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 349190 | 211641 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DR | NP254DR | np25 4dr | np254dr | Monmouthshire | Sir Fynwy | Penrhos STW | 1762 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 343191 | 211046 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DS | NP254DS | np25 4ds | np254ds | Monmouthshire | Sir Fynwy | Penrhos STW | 1331 | 914 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.04 | 9.09 | 10.04 | 342830 | 211558 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DT | NP254DT | np25 4dt | np254dt | Monmouthshire | Sir Fynwy | Penrhos STW | 1836 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 343063 | 210578 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DU | NP254DU | np25 4du | np254du | Monmouthshire | Sir Fynwy | Penrhos STW | 1298 | 914 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.04 | 9.09 | 10.04 | 342730 | 211954 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DW | NP254DW | np25 4dw | np254dw | Monmouthshire | Sir Fynwy | Dingestow STW | 1955 | 882 | 700to900 | 1.77 | 1.29 | 0.95 | 16.44 | 8.77 | 9.69 | 347073 | 211606 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DX | NP254DX | np25 4dx | np254dx | Monmouthshire | Sir Fynwy | Penrhos STW | 2077 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 343576 | 211586 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DY | NP254DY | np25 4dy | np254dy | Monmouthshire | Sir Fynwy | Dingestow STW | 569 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 345324 | 209997 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4DZ | NP254DZ | np25 4dz | np254dz | Monmouthshire | Sir Fynwy | Dingestow STW | 2414 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 343478 | 210115 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4EA | NP254EA | np25 4ea | np254ea | Monmouthshire | Sir Fynwy | Penrhos STW | 2285 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 343683 | 210869 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4EB | NP254EB | np25 4eb | np254eb | Monmouthshire | Sir Fynwy | Dingestow STW | 1948 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 344492 | 211405 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4ED | NP254ED | np25 4ed | np254ed | Monmouthshire | Sir Fynwy | Dingestow STW | 608 | 918 | 900to1200 | 1.84 | 1.34 | 0.99 | 17.11 | 9.13 | 10.09 | 346317 | 210483 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4EE | NP254EE | np25 4ee | np254ee | Monmouthshire | Sir Fynwy | Monmouth STW | 2182 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 349366 | 212052 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4HT | NP254HT | np25 4ht | np254ht | Monmouthshire | Sir Fynwy | Monmouth STW | 2609 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 349359 | 210353 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4HX | NP254HX | np25 4hx | np254hx | Monmouthshire | Sir Fynwy | Monmouth STW | 875 | 923 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.2 | 9.18 | 10.14 | 350797 | 211320 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4HY | NP254HY | np25 4hy | np254hy | Monmouthshire | Sir Fynwy | Monmouth STW | 1566 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 350013 | 211417 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4HZ | NP254HZ | np25 4hz | np254hz | Monmouthshire | Sir Fynwy | Monmouth STW | 2733 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 349224 | 210334 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JB | NP254JB | np25 4jb | np254jb | Monmouthshire | Sir Fynwy | Monmouth STW | 3245 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 349225 | 209515 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JE | NP254JE | np25 4je | np254je | Monmouthshire | Sir Fynwy | Monmouth STW | 3185 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 349180 | 209649 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JF | NP254JF | np25 4jf | np254jf | Monmouthshire | Sir Fynwy | Monmouth STW | 3292 | 959 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.87 | 9.53 | 10.54 | 349362 | 209321 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JG | NP254JG | np25 4jg | np254jg | Monmouthshire | Sir Fynwy | Monmouth STW | 3397 | 959 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.87 | 9.53 | 10.54 | 349441 | 209119 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JH | NP254JH | np25 4jh | np254jh | Monmouthshire | Sir Fynwy | Dingestow STW | 2202 | 874 | 700to900 | 1.75 | 1.28 | 0.94 | 16.29 | 8.69 | 9.6 | 348089 | 210158 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JJ | NP254JJ | np25 4jj | np254jj | Monmouthshire | Sir Fynwy | Trellech STW | 2895 | 922 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.18 | 9.17 | 10.13 | 348274 | 207894 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JL | NP254JL | np25 4jl | np254jl | Monmouthshire | Sir Fynwy | Dingestow STW | 1945 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 347377 | 208798 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JN | NP254JN | np25 4jn | np254jn | Monmouthshire | Sir Fynwy | Monmouth STW | 3271 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 349179 | 209524 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JP | NP254JP | np25 4jp | np254jp | Monmouthshire | Sir Fynwy | Trellech STW | 2743 | 944 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.59 | 9.38 | 10.37 | 347821 | 207288 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JQ | NP254JQ | np25 4jq | np254jq | Monmouthshire | Sir Fynwy | Dingestow STW | 3273 | 959 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.87 | 9.53 | 10.54 | 349022 | 209103 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JR | NP254JR | np25 4jr | np254jr | Monmouthshire | Sir Fynwy | Dingestow STW | 3235 | 959 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.87 | 9.53 | 10.54 | 349037 | 209306 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JS | NP254JS | np25 4js | np254js | Monmouthshire | Sir Fynwy | Trellech STW | 2825 | 1004 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.71 | 9.98 | 11.03 | 349259 | 208250 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4JT | NP254JT | np25 4jt | np254jt | Monmouthshire | Sir Fynwy | Dingestow STW | 2811 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 348290 | 208589 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4LE | NP254LE | np25 4le | np254le | Monmouthshire | Sir Fynwy | Monmouth STW | 206 | 949 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.69 | 9.43 | 10.43 | 351532 | 212001 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4LU | NP254LU | np25 4lu | np254lu | Monmouthshire | Sir Fynwy | Monmouth STW | 2431 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 353661 | 210624 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4LW | NP254LW | np25 4lw | np254lw | Monmouthshire | Sir Fynwy | Monmouth STW | 2590 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 353660 | 210321 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PJ | NP254PJ | np25 4pj | np254pj | Monmouthshire | Sir Fynwy | Trellech STW | 1532 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 348395 | 205783 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PL | NP254PL | np25 4pl | np254pl | Monmouthshire | Sir Fynwy | Trellech STW | 3006 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 347082 | 206544 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PN | NP254PN | np25 4pn | np254pn | Monmouthshire | Sir Fynwy | Llandogo STW | 1311 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 351740 | 203798 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PT | NP254PT | np25 4pt | np254pt | Monmouthshire | Sir Fynwy | WwTW | 998 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 350392 | 203757 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PU | NP254PU | np25 4pu | np254pu | Monmouthshire | Sir Fynwy | WwTW | 477 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 349820 | 203011 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4PW | NP254PW | np25 4pw | np254pw | Monmouthshire | Sir Fynwy | WwTW | 1547 | 1121 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.89 | 11.14 | 12.32 | 351375 | 203815 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QA | NP254QA | np25 4qa | np254qa | Monmouthshire | Sir Fynwy | Trellech STW | 2122 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 347798 | 205786 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QD | NP254QD | np25 4qd | np254qd | Monmouthshire | Sir Fynwy | WwTW | 207 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 350171 | 202969 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QE | NP254QE | np25 4qe | np254qe | Monmouthshire | Sir Fynwy | Llandogo STW | 1544 | 1121 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.89 | 11.14 | 12.32 | 351482 | 203949 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QF | NP254QF | np25 4qf | np254qf | Monmouthshire | Sir Fynwy | WwTW | 521 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 350485 | 203228 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QG | NP254QG | np25 4qg | np254qg | Monmouthshire | Sir Fynwy | Narth WwTW | 333 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 352491 | 206534 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QH | NP254QH | np25 4qh | np254qh | Monmouthshire | Sir Fynwy | Narth WwTW | 194 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 352228 | 206583 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QJ | NP254QJ | np25 4qj | np254qj | Monmouthshire | Sir Fynwy | Narth WwTW | 522 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 352006 | 206318 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QL | NP254QL | np25 4ql | np254ql | Monmouthshire | Sir Fynwy | Narth WwTW | 622 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 352773 | 206422 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QN | NP254QN | np25 4qn | np254qn | Monmouthshire | Sir Fynwy | Narth WwTW | 486 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 352309 | 206291 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QP | NP254QP | np25 4qp | np254qp | Monmouthshire | Sir Fynwy | Narth WwTW | 483 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 352629 | 206463 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QQ | NP254QQ | np25 4qq | np254qq | Monmouthshire | Sir Fynwy | Narth WwTW | 269 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 352474 | 206611 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QR | NP254QR | np25 4qr | np254qr | Monmouthshire | Sir Fynwy | Narth WwTW | 577 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 352741 | 206455 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QS | NP254QS | np25 4qs | np254qs | Monmouthshire | Sir Fynwy | Narth WwTW | 879 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 353073 | 206442 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QT | NP254QT | np25 4qt | np254qt | Monmouthshire | Sir Fynwy | Narth WwTW | 453 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 352283 | 206322 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QU | NP254QU | np25 4qu | np254qu | Monmouthshire | Sir Fynwy | Narth WwTW | 160 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 352381 | 206669 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QW | NP254QW | np25 4qw | np254qw | Monmouthshire | Sir Fynwy | Narth WwTW | 436 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 352388 | 206357 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QX | NP254QX | np25 4qx | np254qx | Monmouthshire | Sir Fynwy | WwTW | 190 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 350124 | 202927 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QY | NP254QY | np25 4qy | np254qy | Monmouthshire | Sir Fynwy | Narth WwTW | 1014 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 352624 | 205828 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4QZ | NP254QZ | np25 4qz | np254qz | Monmouthshire | Sir Fynwy | Narth WwTW | 926 | 1088 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.28 | 10.82 | 11.95 | 352410 | 205861 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4RA | NP254RA | np25 4ra | np254ra | Monmouthshire | Sir Fynwy | Narth WwTW | 1475 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 353276 | 205706 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4RD | NP254RD | np25 4rd | np254rd | Monmouthshire | Sir Fynwy | WwTW | 175 | 1084 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.2 | 10.78 | 11.91 | 350239 | 202947 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4RE | NP254RE | np25 4re | np254re | Monmouthshire | Sir Fynwy | Llandogo STW | 1460 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 353129 | 205535 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4RH | NP254RH | np25 4rh | np254rh | Monmouthshire | Sir Fynwy | Monmouth STW | 3064 | 994 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.53 | 9.88 | 10.92 | 349957 | 209168 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4RJ | NP254RJ | np25 4rj | np254rj | Monmouthshire | Sir Fynwy | Monmouth STW | 2568 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 350249 | 209572 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4RL | NP254RL | np25 4rl | np254rl | Monmouthshire | Sir Fynwy | Trellech STW | 3150 | 959 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.87 | 9.53 | 10.54 | 349340 | 208599 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4RN | NP254RN | np25 4rn | np254rn | Monmouthshire | Sir Fynwy | Narth WwTW | 2125 | 1050 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.57 | 10.44 | 11.54 | 350722 | 208239 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4RP | NP254RP | np25 4rp | np254rp | Monmouthshire | Sir Fynwy | Narth WwTW | 2689 | 1039 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.37 | 10.33 | 11.42 | 350712 | 208971 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4RX | NP254RX | np25 4rx | np254rx | Monmouthshire | Sir Fynwy | Narth WwTW | 1450 | 1032 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.23 | 10.26 | 11.34 | 352722 | 208148 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4RY | NP254RY | np25 4ry | np254ry | Monmouthshire | Sir Fynwy | Narth WwTW | 1305 | 1030 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.2 | 10.24 | 11.32 | 352318 | 208077 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4RZ | NP254RZ | np25 4rz | np254rz | Monmouthshire | Sir Fynwy | Narth WwTW | 992 | 1032 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.23 | 10.26 | 11.34 | 352687 | 207669 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4SA | NP254SA | np25 4sa | np254sa | Monmouthshire | Sir Fynwy | Narth WwTW | 2394 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 352152 | 209165 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4SB | NP254SB | np25 4sb | np254sb | Monmouthshire | Sir Fynwy | Narth WwTW | 2216 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 351928 | 208964 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4SE | NP254SE | np25 4se | np254se | Monmouthshire | Sir Fynwy | Narth WwTW | 2312 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 352103 | 209080 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BZ | NP255BZ | np25 5bz | np255bz | Monmouthshire | Sir Fynwy | Rockfield STW | 1779 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349604 | 213348 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DA | NP255DA | np25 5da | np255da | Monmouthshire | Sir Fynwy | Monmouth STW | 793 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 350760 | 211975 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DB | NP255DB | np25 5db | np255db | Monmouthshire | Sir Fynwy | Monmouth STW | 693 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 350844 | 211879 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DD | NP255DD | np25 5dd | np255dd | Monmouthshire | Sir Fynwy | Monmouth STW | 1627 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349940 | 212126 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DE | NP255DE | np25 5de | np255de | Monmouthshire | Sir Fynwy | Monmouth STW | 1899 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349853 | 212681 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DF | NP255DF | np25 5df | np255df | Monmouthshire | Sir Fynwy | Monmouth STW | 1665 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350033 | 212519 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DG | NP255DG | np25 5dg | np255dg | Monmouthshire | Sir Fynwy | Monmouth STW | 1652 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349931 | 212198 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DH | NP255DH | np25 5dh | np255dh | Monmouthshire | Sir Fynwy | Monmouth STW | 1585 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350016 | 212256 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DJ | NP255DJ | np25 5dj | np255dj | Monmouthshire | Sir Fynwy | Rockfield STW | 1911 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349573 | 213167 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DL | NP255DL | np25 5dl | np255dl | Monmouthshire | Sir Fynwy | Rockfield STW | 1643 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350063 | 214140 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DN | NP255DN | np25 5dn | np255dn | Monmouthshire | Sir Fynwy | Monmouth STW | 2154 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349671 | 212878 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DP | NP255DP | np25 5dp | np255dp | Monmouthshire | Sir Fynwy | Monmouth STW | 2047 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349721 | 212748 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DQ | NP255DQ | np25 5dq | np255dq | Monmouthshire | Sir Fynwy | Monmouth STW | 1496 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350191 | 212457 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DR | NP255DR | np25 5dr | np255dr | Monmouthshire | Sir Fynwy | Rockfield STW | 1795 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349503 | 213260 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DS | NP255DS | np25 5ds | np255ds | Monmouthshire | Sir Fynwy | Rockfield STW | 1818 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 349410 | 213179 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DT | NP255DT | np25 5dt | np255dt | Monmouthshire | Sir Fynwy | Rockfield STW | 2043 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349508 | 212976 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DU | NP255DU | np25 5du | np255du | Monmouthshire | Sir Fynwy | Monmouth STW | 1632 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350058 | 212494 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DW | NP255DW | np25 5dw | np255dw | Monmouthshire | Sir Fynwy | Rockfield STW | 1957 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 349380 | 213008 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DX | NP255DX | np25 5dx | np255dx | Monmouthshire | Sir Fynwy | Monmouth STW | 1416 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350219 | 212323 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DY | NP255DY | np25 5dy | np255dy | Monmouthshire | Sir Fynwy | Rockfield STW | 2061 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 349411 | 212908 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5DZ | NP255DZ | np25 5dz | np255dz | Monmouthshire | Sir Fynwy | Rockfield STW | 2149 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 349457 | 212833 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EA | NP255EA | np25 5ea | np255ea | Monmouthshire | Sir Fynwy | Monmouth STW | 2216 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349551 | 212786 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EB | NP255EB | np25 5eb | np255eb | Monmouthshire | Sir Fynwy | Monmouth STW | 2201 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349588 | 212826 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5ED | NP255ED | np25 5ed | np255ed | Monmouthshire | Sir Fynwy | Rockfield STW | 2210 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349502 | 212786 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EE | NP255EE | np25 5ee | np255ee | Monmouthshire | Sir Fynwy | Monmouth STW | 1580 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349997 | 212167 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EF | NP255EF | np25 5ef | np255ef | Monmouthshire | Sir Fynwy | Monmouth STW | 1556 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349992 | 212012 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EG | NP255EG | np25 5eg | np255eg | Monmouthshire | Sir Fynwy | Monmouth STW | 1602 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349951 | 212049 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EH | NP255EH | np25 5eh | np255eh | Monmouthshire | Sir Fynwy | Monmouth STW | 1603 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349958 | 212095 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EJ | NP255EJ | np25 5ej | np255ej | Monmouthshire | Sir Fynwy | Monmouth STW | 748 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 350808 | 211983 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EL | NP255EL | np25 5el | np255el | Monmouthshire | Sir Fynwy | Monmouth STW | 1663 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349894 | 212080 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EN | NP255EN | np25 5en | np255en | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 3557 | 875 | 700to900 | 1.75 | 1.28 | 0.94 | 16.31 | 8.7 | 9.61 | 343284 | 214671 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EP | NP255EP | np25 5ep | np255ep | Monmouthshire | Sir Fynwy | Penrhos STW | 2783 | 897 | 700to900 | 1.8 | 1.31 | 0.96 | 16.72 | 8.92 | 9.86 | 343842 | 213042 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EQ | NP255EQ | np25 5eq | np255eq | Monmouthshire | Sir Fynwy | Monmouth STW | 2026 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349886 | 212975 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5ER | NP255ER | np25 5er | np255er | Monmouthshire | Sir Fynwy | Monmouth STW | 1308 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350434 | 212505 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5ES | NP255ES | np25 5es | np255es | Monmouthshire | Sir Fynwy | Monmouth STW | 1292 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350406 | 212428 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5ET | NP255ET | np25 5et | np255et | Monmouthshire | Sir Fynwy | Monmouth STW | 1374 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350225 | 212218 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EU | NP255EU | np25 5eu | np255eu | Monmouthshire | Sir Fynwy | Monmouth STW | 1369 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350215 | 212168 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EW | NP255EW | np25 5ew | np255ew | Monmouthshire | Sir Fynwy | Rockfield STW | 2114 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349538 | 212912 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EX | NP255EX | np25 5ex | np255ex | Monmouthshire | Sir Fynwy | Monmouth STW | 1116 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 350524 | 212272 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EY | NP255EY | np25 5ey | np255ey | Monmouthshire | Sir Fynwy | Monmouth STW | 1178 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350491 | 212346 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5EZ | NP255EZ | np25 5ez | np255ez | Monmouthshire | Sir Fynwy | Monmouth STW | 1042 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 350590 | 212239 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5FA | NP255FA | np25 5fa | np255fa | Monmouthshire | Sir Fynwy | Monmouth STW | 1572 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350098 | 212438 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5FB | NP255FB | np25 5fb | np255fb | Monmouthshire | Sir Fynwy | Monmouth STW | 876 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 350657 | 211828 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5FD | NP255FD | np25 5fd | np255fd | Monmouthshire | Sir Fynwy | Monmouth STW | 1977 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349770 | 212690 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5FE | NP255FE | np25 5fe | np255fe | Monmouthshire | Sir Fynwy | Monmouth STW | 1836 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349970 | 212759 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5FF | NP255FF | np25 5ff | np255ff | Monmouthshire | Sir Fynwy | Monmouth STW | 1864 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349921 | 212732 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5FG | NP255FG | np25 5fg | np255fg | Monmouthshire | Sir Fynwy | Monmouth STW | 1849 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349882 | 212628 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5FH | NP255FH | np25 5fh | np255fh | Monmouthshire | Sir Fynwy | Monmouth STW | 1822 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349906 | 212615 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5FJ | NP255FJ | np25 5fj | np255fj | Monmouthshire | Sir Fynwy | Monmouth STW | 1734 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349972 | 212551 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5FL | NP255FL | np25 5fl | np255fl | Monmouthshire | Sir Fynwy | Monmouth STW | 969 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 350565 | 211854 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5FN | NP255FN | np25 5fn | np255fn | Monmouthshire | Sir Fynwy | Monmouth STW | 1586 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350112 | 212500 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5FP | NP255FP | np25 5fp | np255fp | Monmouthshire | Sir Fynwy | Monmouth STW | 947 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 350632 | 212087 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5GA | NP255GA | np25 5ga | np255ga | Monmouthshire | Sir Fynwy | Monmouth STW | 2014 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349783 | 212792 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5GB | NP255GB | np25 5gb | np255gb | Monmouthshire | Sir Fynwy | Rockfield STW | 1686 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 349276 | 213259 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5GD | NP255GD | np25 5gd | np255gd | Monmouthshire | Sir Fynwy | Rockfield STW | 1682 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 349348 | 213300 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5GE | NP255GE | np25 5ge | np255ge | Monmouthshire | Sir Fynwy | Rockfield STW | 1782 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 349329 | 213178 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5GF | NP255GF | np25 5gf | np255gf | Monmouthshire | Sir Fynwy | Rockfield STW | 1736 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 349274 | 213203 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HA | NP255HA | np25 5ha | np255ha | Monmouthshire | Sir Fynwy | Monmouth STW | 1301 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350369 | 212377 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HB | NP255HB | np25 5hb | np255hb | Monmouthshire | Sir Fynwy | Rockfield STW | 2968 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 345588 | 214616 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HD | NP255HD | np25 5hd | np255hd | Monmouthshire | Sir Fynwy | Rockfield STW | 2834 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 345722 | 214952 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HE | NP255HE | np25 5he | np255he | Monmouthshire | Sir Fynwy | Rockfield STW | 3232 | 886 | 700to900 | 1.77 | 1.3 | 0.95 | 16.51 | 8.81 | 9.73 | 345320 | 214693 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HF | NP255HF | np25 5hf | np255hf | Monmouthshire | Sir Fynwy | Rockfield STW | 3281 | 886 | 700to900 | 1.77 | 1.3 | 0.95 | 16.51 | 8.81 | 9.73 | 345271 | 214735 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HG | NP255HG | np25 5hg | np255hg | Monmouthshire | Sir Fynwy | Rockfield STW | 2933 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 345626 | 214564 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HH | NP255HH | np25 5hh | np255hh | Monmouthshire | Sir Fynwy | Rockfield STW | 3767 | 894 | 700to900 | 1.79 | 1.31 | 0.96 | 16.66 | 8.89 | 9.82 | 344800 | 214436 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HJ | NP255HJ | np25 5hj | np255hj | Monmouthshire | Sir Fynwy | Rockfield STW | 3314 | 894 | 700to900 | 1.79 | 1.31 | 0.96 | 16.66 | 8.89 | 9.82 | 345462 | 213581 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HL | NP255HL | np25 5hl | np255hl | Monmouthshire | Sir Fynwy | Penrhos STW | 2791 | 887 | 700to900 | 1.78 | 1.3 | 0.95 | 16.53 | 8.82 | 9.75 | 343117 | 213814 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HN | NP255HN | np25 5hn | np255hn | Monmouthshire | Sir Fynwy | Penrhos STW | 2832 | 887 | 700to900 | 1.78 | 1.3 | 0.95 | 16.53 | 8.82 | 9.75 | 342558 | 214166 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HP | NP255HP | np25 5hp | np255hp | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 2625 | 895 | 700to900 | 1.79 | 1.31 | 0.96 | 16.68 | 8.9 | 9.83 | 342340 | 214818 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HQ | NP255HQ | np25 5hq | np255hq | Monmouthshire | Sir Fynwy | Rockfield STW | 3121 | 886 | 700to900 | 1.77 | 1.3 | 0.95 | 16.51 | 8.81 | 9.73 | 345434 | 214623 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HR | NP255HR | np25 5hr | np255hr | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 2484 | 895 | 700to900 | 1.79 | 1.31 | 0.96 | 16.68 | 8.9 | 9.83 | 342125 | 215204 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HS | NP255HS | np25 5hs | np255hs | Monmouthshire | Sir Fynwy | Rockfield STW | 1533 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349692 | 213758 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HT | NP255HT | np25 5ht | np255ht | Monmouthshire | Sir Fynwy | Rockfield STW | 2669 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 345931 | 214269 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5HW | NP255HW | np25 5hw | np255hw | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 3233 | 886 | 700to900 | 1.77 | 1.3 | 0.95 | 16.51 | 8.81 | 9.73 | 342620 | 215996 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5JA | NP255JA | np25 5ja | np255ja | Monmouthshire | Sir Fynwy | Monmouth STW | 1835 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349774 | 212317 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5JB | NP255JB | np25 5jb | np255jb | Monmouthshire | Sir Fynwy | Monmouth STW | 1743 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349870 | 212318 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5LB | NP255LB | np25 5lb | np255lb | Monmouthshire | Sir Fynwy | Rockfield STW | 2308 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 350850 | 214960 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5LD | NP255LD | np25 5ld | np255ld | Monmouthshire | Sir Fynwy | Rockfield STW | 2348 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 350886 | 215004 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5LE | NP255LE | np25 5le | np255le | Monmouthshire | Sir Fynwy | Rockfield STW | 2303 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 350847 | 214939 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5LF | NP255LF | np25 5lf | np255lf | Monmouthshire | Sir Fynwy | Rockfield STW | 2061 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 350604 | 214938 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NF | NP255NF | np25 5nf | np255nf | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 3310 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 343023 | 217873 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NG | NP255NG | np25 5ng | np255ng | Monmouthshire | Sir Fynwy | Rockfield STW | 2953 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 345736 | 215672 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NH | NP255NH | np25 5nh | np255nh | Monmouthshire | Sir Fynwy | Rockfield STW | 1383 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 347168 | 214829 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NJ | NP255NJ | np25 5nj | np255nj | Monmouthshire | Sir Fynwy | Rockfield STW | 2815 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 345922 | 215785 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NL | NP255NL | np25 5nl | np255nl | Monmouthshire | Sir Fynwy | Rockfield STW | 4384 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 344278 | 215756 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NN | NP255NN | np25 5nn | np255nn | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 4421 | 885 | 700to900 | 1.77 | 1.3 | 0.95 | 16.5 | 8.8 | 9.72 | 344897 | 219193 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NP | NP255NP | np25 5np | np255np | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 4450 | 885 | 700to900 | 1.77 | 1.3 | 0.95 | 16.5 | 8.8 | 9.72 | 344916 | 219146 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NQ | NP255NQ | np25 5nq | np255nq | Monmouthshire | Sir Fynwy | Rockfield STW | 2937 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 345740 | 215631 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NR | NP255NR | np25 5nr | np255nr | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 4521 | 885 | 700to900 | 1.77 | 1.3 | 0.95 | 16.5 | 8.8 | 9.72 | 344957 | 219007 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NS | NP255NS | np25 5ns | np255ns | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 4597 | 885 | 700to900 | 1.77 | 1.3 | 0.95 | 16.5 | 8.8 | 9.72 | 345103 | 219338 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NT | NP255NT | np25 5nt | np255nt | Monmouthshire | Sir Fynwy | Rockfield STW | 4648 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 344794 | 217515 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NU | NP255NU | np25 5nu | np255nu | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 4113 | 895 | 700to900 | 1.79 | 1.31 | 0.96 | 16.68 | 8.9 | 9.83 | 344160 | 218089 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NW | NP255NW | np25 5nw | np255nw | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 4412 | 885 | 700to900 | 1.77 | 1.3 | 0.95 | 16.5 | 8.8 | 9.72 | 344876 | 219141 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NX | NP255NX | np25 5nx | np255nx | Monmouthshire | Sir Fynwy | Rockfield STW | 3755 | 893 | 700to900 | 1.79 | 1.31 | 0.96 | 16.64 | 8.88 | 9.81 | 345264 | 216595 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5NY | NP255NY | np25 5ny | np255ny | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 4284 | 885 | 700to900 | 1.77 | 1.3 | 0.95 | 16.5 | 8.8 | 9.72 | 344678 | 218883 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5PW | NP255PW | np25 5pw | np255pw | Monmouthshire | Sir Fynwy | Rockfield STW | 1674 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 347468 | 216057 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5PX | NP255PX | np25 5px | np255px | Monmouthshire | Sir Fynwy | Rockfield STW | 1835 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 347087 | 215886 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5PY | NP255PY | np25 5py | np255py | Monmouthshire | Sir Fynwy | Rockfield STW | 222 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 348457 | 214578 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5PZ | NP255PZ | np25 5pz | np255pz | Monmouthshire | Sir Fynwy | Rockfield STW | 248 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 348396 | 214586 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5QA | NP255QA | np25 5qa | np255qa | Monmouthshire | Sir Fynwy | Rockfield STW | 309 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 348244 | 214823 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5QB | NP255QB | np25 5qb | np255qb | Monmouthshire | Sir Fynwy | Rockfield STW | 350 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 348249 | 214958 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5QD | NP255QD | np25 5qd | np255qd | Monmouthshire | Sir Fynwy | Rockfield STW | 939 | 848 | 700to900 | 1.7 | 1.24 | 0.91 | 15.81 | 8.43 | 9.32 | 348416 | 215709 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5QE | NP255QE | np25 5qe | np255qe | Monmouthshire | Sir Fynwy | Rockfield STW | 782 | 860 | 700to900 | 1.72 | 1.26 | 0.92 | 16.03 | 8.55 | 9.45 | 347963 | 215296 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5QF | NP255QF | np25 5qf | np255qf | Monmouthshire | Sir Fynwy | Rockfield STW | 2871 | 876 | 700to900 | 1.75 | 1.28 | 0.94 | 16.33 | 8.71 | 9.62 | 346397 | 216677 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5QG | NP255QG | np25 5qg | np255qg | Monmouthshire | Sir Fynwy | Rockfield STW | 2636 | 856 | 700to900 | 1.71 | 1.25 | 0.92 | 15.95 | 8.51 | 9.4 | 346986 | 216901 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5QH | NP255QH | np25 5qh | np255qh | Monmouthshire | Sir Fynwy | Rockfield STW | 2066 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 347233 | 216371 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5QQ | NP255QQ | np25 5qq | np255qq | Monmouthshire | Sir Fynwy | Rockfield STW | 3215 | 856 | 700to900 | 1.71 | 1.25 | 0.92 | 15.95 | 8.51 | 9.4 | 346725 | 217425 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5QX | NP255QX | np25 5qx | np255qx | Monmouthshire | Sir Fynwy | Rockfield STW | 2086 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 350622 | 215014 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5QY | NP255QY | np25 5qy | np255qy | Monmouthshire | Sir Fynwy | Rockfield STW | 1997 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 350499 | 215210 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5QZ | NP255QZ | np25 5qz | np255qz | Monmouthshire | Sir Fynwy | Rockfield STW | 2112 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 350612 | 215231 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5RA | NP255RA | np25 5ra | np255ra | Monmouthshire | Sir Fynwy | Rockfield STW | 2595 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 351144 | 214790 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5RB | NP255RB | np25 5rb | np255rb | Monmouthshire | Sir Fynwy | Rockfield STW | 1821 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 350280 | 215345 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5RE | NP255RE | np25 5re | np255re | Monmouthshire | Sir Fynwy | Rockfield STW | 2442 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 350952 | 215217 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5RF | NP255RF | np25 5rf | np255rf | Monmouthshire | Sir Fynwy | Rockfield STW | 2548 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 350691 | 216160 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5RZ | NP255RZ | np25 5rz | np255rz | Monmouthshire | Sir Fynwy | Rockfield STW | 2647 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 351070 | 215587 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5SA | NP255SA | np25 5sa | np255sa | Monmouthshire | Sir Fynwy | Monmouth STW | 1927 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349890 | 212802 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5SB | NP255SB | np25 5sb | np255sb | Monmouthshire | Sir Fynwy | Monmouth STW | 1880 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349830 | 212593 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5SD | NP255SD | np25 5sd | np255sd | Monmouthshire | Sir Fynwy | Monmouth STW | 2116 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349740 | 212918 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5SR | NP255SR | np25 5sr | np255sr | Monmouthshire | Sir Fynwy | Rockfield STW | 1551 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349543 | 213589 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5SS | NP255SS | np25 5ss | np255ss | Monmouthshire | Sir Fynwy | Rockfield STW | 1637 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349829 | 213759 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5ST | NP255ST | np25 5st | np255st | Monmouthshire | Sir Fynwy | Rockfield STW | 828 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 348879 | 214021 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5SU | NP255SU | np25 5su | np255su | Monmouthshire | Sir Fynwy | Rockfield STW | 474 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 348641 | 214315 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5SW | NP255SW | np25 5sw | np255sw | Monmouthshire | Sir Fynwy | Rockfield STW | 1254 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 347359 | 214388 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5SX | NP255SX | np25 5sx | np255sx | Monmouthshire | Sir Fynwy | Rockfield STW | 2462 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 346093 | 214633 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5SY | NP255SY | np25 5sy | np255sy | Monmouthshire | Sir Fynwy | Rockfield STW | 355 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 348525 | 214426 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5SZ | NP255SZ | np25 5sz | np255sz | Monmouthshire | Sir Fynwy | Rockfield STW | 2051 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 346511 | 214566 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5TN | NP255TN | np25 5tn | np255tn | Monmouthshire | Sir Fynwy | Monmouth STW | 1368 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350181 | 212007 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5TQ | NP255TQ | np25 5tq | np255tq | Monmouthshire | Sir Fynwy | Monmouth STW | 1502 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350036 | 211927 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5TR | NP255TR | np25 5tr | np255tr | Monmouthshire | Sir Fynwy | Monmouth STW | 1424 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350123 | 211997 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5TS | NP255TS | np25 5ts | np255ts | Monmouthshire | Sir Fynwy | Monmouth STW | 1511 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350035 | 211993 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5TW | NP255TW | np25 5tw | np255tw | Monmouthshire | Sir Fynwy | Monmouth STW | 1859 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349686 | 212006 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UA | NP255UA | np25 5ua | np255ua | Monmouthshire | Sir Fynwy | Monmouth STW | 1273 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350273 | 211982 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UB | NP255UB | np25 5ub | np255ub | Monmouthshire | Sir Fynwy | Monmouth STW | 1285 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350274 | 212053 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UD | NP255UD | np25 5ud | np255ud | Monmouthshire | Sir Fynwy | Monmouth STW | 1215 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350355 | 212095 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UE | NP255UE | np25 5ue | np255ue | Monmouthshire | Sir Fynwy | Monmouth STW | 1156 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350409 | 212068 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UF | NP255UF | np25 5uf | np255uf | Monmouthshire | Sir Fynwy | Monmouth STW | 1150 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350427 | 212111 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UG | NP255UG | np25 5ug | np255ug | Monmouthshire | Sir Fynwy | Monmouth STW | 1067 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 350521 | 212135 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UH | NP255UH | np25 5uh | np255uh | Monmouthshire | Sir Fynwy | Monmouth STW | 1055 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 350505 | 212033 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UJ | NP255UJ | np25 5uj | np255uj | Monmouthshire | Sir Fynwy | Monmouth STW | 1121 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350440 | 212045 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UP | NP255UP | np25 5up | np255up | Monmouthshire | Sir Fynwy | Rockfield STW | 2459 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 349109 | 212386 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UQ | NP255UQ | np25 5uq | np255uq | Monmouthshire | Sir Fynwy | Rockfield STW | 2452 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 349078 | 212386 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UR | NP255UR | np25 5ur | np255ur | Monmouthshire | Sir Fynwy | Rockfield STW | 2363 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 349188 | 212506 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5US | NP255US | np25 5us | np255us | Monmouthshire | Sir Fynwy | Rockfield STW | 2281 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 349135 | 212576 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UT | NP255UT | np25 5ut | np255ut | Monmouthshire | Sir Fynwy | Monmouth STW | 2363 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 349248 | 212396 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UW | NP255UW | np25 5uw | np255uw | Monmouthshire | Sir Fynwy | Monmouth STW | 2309 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 349262 | 212214 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UX | NP255UX | np25 5ux | np255ux | Monmouthshire | Sir Fynwy | Monmouth STW | 1561 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350039 | 212250 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UY | NP255UY | np25 5uy | np255uy | Monmouthshire | Sir Fynwy | Monmouth STW | 2394 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 349193 | 212302 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5UZ | NP255UZ | np25 5uz | np255uz | Monmouthshire | Sir Fynwy | Monmouth STW | 2403 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 349180 | 212283 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5WA | NP255WA | np25 5wa | np255wa | Monmouthshire | Sir Fynwy | Rockfield STW | 2281 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 349099 | 212567 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5XT | NP255XT | np25 5xt | np255xt | Monmouthshire | Sir Fynwy | Monmouth STW | 1794 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 351012 | 213511 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5ZG | NP255ZG | np25 5zg | np255zg | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 9BD | NP259BD | np25 9bd | np259bd | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 9BF | NP259BF | np25 9bf | np259bf | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 9BN | NP259BN | np25 9bn | np259bn | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 9BW | NP259BW | np25 9bw | np259bw | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 9BY | NP259BY | np25 9by | np259by | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 9DA | NP259DA | np25 9da | np259da | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 9DB | NP259DB | np25 9db | np259db | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 9DD | NP259DD | np25 9dd | np259dd | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 9DE | NP259DE | np25 9de | np259de | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4SF | NP254SF | np25 4sf | np254sf | Monmouthshire | Sir Fynwy | Narth WwTW | 2101 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 352015 | 208860 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4SP | NP254SP | np25 4sp | np254sp | Monmouthshire | Sir Fynwy | Narth WwTW | 2365 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 351976 | 209121 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4SQ | NP254SQ | np25 4sq | np254sq | Monmouthshire | Sir Fynwy | Llandogo STW | 361 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352837 | 204391 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4SR | NP254SR | np25 4sr | np254sr | Monmouthshire | Sir Fynwy | Llandogo STW | 307 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352829 | 204320 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4SY | NP254SY | np25 4sy | np254sy | Monmouthshire | Sir Fynwy | Llandogo STW | 411 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352616 | 204153 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4SZ | NP254SZ | np25 4sz | np254sz | Monmouthshire | Sir Fynwy | Llandogo STW | 457 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352567 | 204141 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TA | NP254TA | np25 4ta | np254ta | Monmouthshire | Sir Fynwy | Llandogo STW | 500 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352532 | 203971 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TB | NP254TB | np25 4tb | np254tb | Monmouthshire | Sir Fynwy | Llandogo STW | 486 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352537 | 204032 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TD | NP254TD | np25 4td | np254td | Monmouthshire | Sir Fynwy | Llandogo STW | 506 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352563 | 203863 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TE | NP254TE | np25 4te | np254te | Monmouthshire | Sir Fynwy | Llandogo STW | 637 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 352425 | 203853 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TF | NP254TF | np25 4tf | np254tf | Monmouthshire | Sir Fynwy | Llandogo STW | 719 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 352327 | 203891 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TG | NP254TG | np25 4tg | np254tg | Monmouthshire | Sir Fynwy | Llandogo STW | 529 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352519 | 204248 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TH | NP254TH | np25 4th | np254th | Monmouthshire | Sir Fynwy | Narth WwTW | 1826 | 977 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.21 | 9.71 | 10.73 | 353811 | 205811 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TJ | NP254TJ | np25 4tj | np254tj | Monmouthshire | Sir Fynwy | Llandogo STW | 345 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352678 | 204128 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TL | NP254TL | np25 4tl | np254tl | Monmouthshire | Sir Fynwy | Llandogo STW | 488 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352540 | 204168 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TN | NP254TN | np25 4tn | np254tn | Monmouthshire | Sir Fynwy | Llandogo STW | 1437 | 1041 | 900to1200 | 2.08 | 1.52 | 1.12 | 19.4 | 10.35 | 11.44 | 352842 | 202655 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TP | NP254TP | np25 4tp | np254tp | Monmouthshire | Sir Fynwy | Llandogo STW | 676 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 352364 | 204242 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TQ | NP254TQ | np25 4tq | np254tq | Monmouthshire | Sir Fynwy | Llandogo STW | 649 | 1075 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.04 | 10.69 | 11.81 | 352383 | 203958 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TR | NP254TR | np25 4tr | np254tr | Monmouthshire | Sir Fynwy | Llandogo STW | 275 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352904 | 204329 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TS | NP254TS | np25 4ts | np254ts | Monmouthshire | Sir Fynwy | Llandogo STW | 849 | 993 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.51 | 9.87 | 10.91 | 353579 | 204718 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TT | NP254TT | np25 4tt | np254tt | Monmouthshire | Sir Fynwy | Narth WwTW | 1267 | 986 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.38 | 9.8 | 10.83 | 353517 | 206621 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TU | NP254TU | np25 4tu | np254tu | Monmouthshire | Sir Fynwy | Narth WwTW | 1195 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 353417 | 206475 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TW | NP254TW | np25 4tw | np254tw | Monmouthshire | Sir Fynwy | Llandogo STW | 265 | 1018 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.97 | 10.12 | 11.18 | 352977 | 204341 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TX | NP254TX | np25 4tx | np254tx | Monmouthshire | Sir Fynwy | Narth WwTW | 325 | 1028 | 900to1200 | 2.06 | 1.51 | 1.1 | 19.16 | 10.22 | 11.29 | 352467 | 207025 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TY | NP254TY | np25 4ty | np254ty | Monmouthshire | Sir Fynwy | Narth WwTW | 1070 | 1079 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.11 | 10.73 | 11.85 | 351426 | 207443 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4TZ | NP254TZ | np25 4tz | np254tz | Monmouthshire | Sir Fynwy | Narth WwTW | 1154 | 1030 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.2 | 10.24 | 11.32 | 351545 | 207679 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4UA | NP254UA | np25 4ua | np254ua | Monmouthshire | Sir Fynwy | Trellech STW | 1108 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 349554 | 206552 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 4XJ | NP254XJ | np25 4xj | np254xj | Monmouthshire | Sir Fynwy | Monmouth STW | 1383 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 350890 | 213019 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AA | NP255AA | np25 5aa | np255aa | Monmouthshire | Sir Fynwy | Monmouth STW | 1347 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350382 | 212496 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AB | NP255AB | np25 5ab | np255ab | Monmouthshire | Sir Fynwy | Monmouth STW | 1377 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350373 | 212537 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AD | NP255AD | np25 5ad | np255ad | Monmouthshire | Sir Fynwy | Monmouth STW | 1410 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350323 | 212519 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AE | NP255AE | np25 5ae | np255ae | Monmouthshire | Sir Fynwy | Monmouth STW | 1393 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350323 | 212485 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AF | NP255AF | np25 5af | np255af | Monmouthshire | Sir Fynwy | Monmouth STW | 1440 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350278 | 212502 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AG | NP255AG | np25 5ag | np255ag | Monmouthshire | Sir Fynwy | Monmouth STW | 1335 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350322 | 212359 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AH | NP255AH | np25 5ah | np255ah | Monmouthshire | Sir Fynwy | Monmouth STW | 1509 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350156 | 212414 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AJ | NP255AJ | np25 5aj | np255aj | Monmouthshire | Sir Fynwy | Monmouth STW | 1409 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350284 | 212449 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AL | NP255AL | np25 5al | np255al | Monmouthshire | Sir Fynwy | Monmouth STW | 1250 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350408 | 212340 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AN | NP255AN | np25 5an | np255an | Monmouthshire | Sir Fynwy | Monmouth STW | 2003 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349876 | 212921 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AP | NP255AP | np25 5ap | np255ap | Monmouthshire | Sir Fynwy | Monmouth STW | 1080 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 350540 | 212222 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AQ | NP255AQ | np25 5aq | np255aq | Monmouthshire | Sir Fynwy | Monmouth STW | 1176 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350458 | 212273 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AR | NP255AR | np25 5ar | np255ar | Monmouthshire | Sir Fynwy | Monmouth STW | 1479 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350113 | 212209 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AS | NP255AS | np25 5as | np255as | Monmouthshire | Sir Fynwy | Monmouth STW | 1576 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350220 | 212667 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AT | NP255AT | np25 5at | np255at | Monmouthshire | Sir Fynwy | Monmouth STW | 2163 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349583 | 212731 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AU | NP255AU | np25 5au | np255au | Monmouthshire | Sir Fynwy | Monmouth STW | 1784 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350108 | 212868 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AW | NP255AW | np25 5aw | np255aw | Monmouthshire | Sir Fynwy | Monmouth STW | 2075 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349835 | 212987 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AX | NP255AX | np25 5ax | np255ax | Monmouthshire | Sir Fynwy | Rockfield STW | 2074 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349742 | 213084 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AY | NP255AY | np25 5ay | np255ay | Monmouthshire | Sir Fynwy | Monmouth STW | 2085 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349882 | 213068 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5AZ | NP255AZ | np25 5az | np255az | Monmouthshire | Sir Fynwy | Rockfield STW | 2077 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349827 | 213143 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BA | NP255BA | np25 5ba | np255ba | Monmouthshire | Sir Fynwy | Monmouth STW | 1916 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350054 | 213013 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BB | NP255BB | np25 5bb | np255bb | Monmouthshire | Sir Fynwy | Monmouth STW | 1872 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350020 | 212898 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BD | NP255BD | np25 5bd | np255bd | Monmouthshire | Sir Fynwy | Monmouth STW | 2059 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349853 | 212986 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BE | NP255BE | np25 5be | np255be | Monmouthshire | Sir Fynwy | Monmouth STW | 1968 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349978 | 213001 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BG | NP255BG | np25 5bg | np255bg | Monmouthshire | Sir Fynwy | Monmouth STW | 1243 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350373 | 212242 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BJ | NP255BJ | np25 5bj | np255bj | Monmouthshire | Sir Fynwy | Monmouth STW | 1462 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350179 | 212347 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BL | NP255BL | np25 5bl | np255bl | Monmouthshire | Sir Fynwy | Monmouth STW | 1666 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350099 | 212644 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BN | NP255BN | np25 5bn | np255bn | Monmouthshire | Sir Fynwy | Monmouth STW | 1336 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350301 | 212312 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BP | NP255BP | np25 5bp | np255bp | Monmouthshire | Sir Fynwy | Monmouth STW | 1711 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349942 | 212424 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BQ | NP255BQ | np25 5bq | np255bq | Monmouthshire | Sir Fynwy | Monmouth STW | 1614 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 350045 | 212422 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BR | NP255BR | np25 5br | np255br | Monmouthshire | Sir Fynwy | Monmouth STW | 1577 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 350152 | 212557 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BS | NP255BS | np25 5bs | np255bs | Monmouthshire | Sir Fynwy | Rockfield STW | 1958 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349719 | 213210 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BT | NP255BT | np25 5bt | np255bt | Monmouthshire | Sir Fynwy | Rockfield STW | 1985 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349815 | 213251 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BU | NP255BU | np25 5bu | np255bu | Monmouthshire | Sir Fynwy | Rockfield STW | 1931 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349667 | 213206 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BW | NP255BW | np25 5bw | np255bw | Monmouthshire | Sir Fynwy | Monmouth STW | 1686 | 865 | 700to900 | 1.73 | 1.27 | 0.93 | 16.12 | 8.6 | 9.5 | 349951 | 212379 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BX | NP255BX | np25 5bx | np255bx | Monmouthshire | Sir Fynwy | Rockfield STW | 1879 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349557 | 213195 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP25 5BY | NP255BY | np25 5by | np255by | Monmouthshire | Sir Fynwy | Rockfield STW | 1814 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 349694 | 213373 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 7LB | NP77LB | np7 7lb | np77lb | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1819 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 331291 | 219784 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7LD | NP77LD | np7 7ld | np77ld | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1830 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 331338 | 219777 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NB | NP77NB | np7 7nb | np77nb | Monmouthshire | Sir Fynwy | Cwmyoy STW | 651 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 331465 | 221010 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7ND | NP77ND | np7 7nd | np77nd | Monmouthshire | Sir Fynwy | Cwmyoy STW | 125 | 1155 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.53 | 11.48 | 12.69 | 331153 | 221719 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NE | NP77NE | np7 7ne | np77ne | Monmouthshire | Sir Fynwy | Cwmyoy STW | 322 | 1155 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.53 | 11.48 | 12.69 | 330943 | 221807 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NF | NP77NF | np7 7nf | np77nf | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1620 | 1246 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.22 | 12.39 | 13.69 | 329899 | 222578 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NG | NP77NG | np7 7ng | np77ng | Monmouthshire | Sir Fynwy | Cwmyoy STW | 3429 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 329007 | 224243 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NH | NP77NH | np7 7nh | np77nh | Monmouthshire | Sir Fynwy | Cwmyoy STW | 4457 | 1247 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.24 | 12.4 | 13.7 | 329292 | 225631 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NL | NP77NL | np7 7nl | np77nl | Monmouthshire | Sir Fynwy | Cwmyoy STW | 5497 | 1246 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.22 | 12.39 | 13.69 | 329327 | 226770 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NN | NP77NN | np7 7nn | np77nn | Monmouthshire | Sir Fynwy | Cwmyoy STW | 6814 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 328610 | 227904 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NP | NP77NP | np7 7np | np77np | Powys | Powys | Velindre STW | 8230 | 1465 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.31 | 14.56 | 16.1 | 325197 | 232188 | Brecon Beacons National Park LPA | PO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NR | NP77NR | np7 7nr | np77nr | Monmouthshire | Sir Fynwy | Cwmyoy STW | 2761 | 1191 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.2 | 11.84 | 13.09 | 329698 | 223922 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NS | NP77NS | np7 7ns | np77ns | Monmouthshire | Sir Fynwy | Cwmyoy STW | 2419 | 1246 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.22 | 12.39 | 13.69 | 329555 | 223381 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NT | NP77NT | np7 7nt | np77nt | Monmouthshire | Sir Fynwy | Cwmyoy STW | 2078 | 1246 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.22 | 12.39 | 13.69 | 330147 | 223397 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NU | NP77NU | np7 7nu | np77nu | Monmouthshire | Sir Fynwy | Cwmyoy STW | 904 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 331116 | 222501 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NW | NP77NW | np7 7nw | np77nw | Monmouthshire | Sir Fynwy | Cwmyoy STW | 9228 | 1354 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.24 | 13.46 | 14.88 | 327004 | 229821 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7NY | NP77NY | np7 7ny | np77ny | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1033 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 331822 | 222417 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7PA | NP77PA | np7 7pa | np77pa | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1101 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 330215 | 222111 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7PB | NP77PB | np7 7pb | np77pb | Monmouthshire | Sir Fynwy | Pandy STW | 338 | 1047 | 900to1200 | 2.1 | 1.53 | 1.12 | 19.51 | 10.41 | 11.5 | 333256 | 222628 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7PD | NP77PD | np7 7pd | np77pd | Monmouthshire | Sir Fynwy | Pandy STW | 992 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 332610 | 222443 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7PE | NP77PE | np7 7pe | np77pe | Monmouthshire | Sir Fynwy | Pandy STW | 1290 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 332396 | 222207 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7PF | NP77PF | np7 7pf | np77pf | Monmouthshire | Sir Fynwy | Pandy STW | 227 | 1047 | 900to1200 | 2.1 | 1.53 | 1.12 | 19.51 | 10.41 | 11.5 | 333306 | 222761 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7PG | NP77PG | np7 7pg | np77pg | Monmouthshire | Sir Fynwy | Pandy STW | 667 | 1047 | 900to1200 | 2.1 | 1.53 | 1.12 | 19.51 | 10.41 | 11.5 | 332853 | 222888 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 7PH | NP77PH | np7 7ph | np77ph | Monmouthshire | Sir Fynwy | Pandy STW | 2027 | 1154 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.51 | 11.47 | 12.68 | 332467 | 224575 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8AA | NP78AA | np7 8aa | np78aa | Monmouthshire | Sir Fynwy | Llanvapley STW | 3455 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 333492 | 216268 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8AB | NP78AB | np7 8ab | np78ab | Monmouthshire | Sir Fynwy | Llanvapley STW | 3510 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 333187 | 215976 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8AD | NP78AD | np7 8ad | np78ad | Monmouthshire | Sir Fynwy | Llanvapley STW | 3529 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 333215 | 216048 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8AF | NP78AF | np7 8af | np78af | Monmouthshire | Sir Fynwy | Grosmont WwTW | 585 | 920 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.15 | 9.15 | 10.11 | 340319 | 224320 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8AG | NP78AG | np7 8ag | np78ag | Monmouthshire | Sir Fynwy | Llanvapley STW | 3097 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 334368 | 216548 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8AH | NP78AH | np7 8ah | np78ah | Monmouthshire | Sir Fynwy | Llanvapley STW | 2426 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 335209 | 216223 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8AL | NP78AL | np7 8al | np78al | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 2289 | 940 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.52 | 9.34 | 10.33 | 339672 | 217988 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8AN | NP78AN | np7 8an | np78an | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1742 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 332459 | 220407 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8AP | NP78AP | np7 8ap | np78ap | Monmouthshire | Sir Fynwy | Llanvapley STW | 3813 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 333179 | 216455 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8AW | NP78AW | np7 8aw | np78aw | Monmouthshire | Sir Fynwy | Llanvapley STW | 3690 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 334048 | 217046 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8BE | NP78BE | np7 8be | np78be | Monmouthshire | Sir Fynwy | Llanfoist WwTW | 2978 | 1030 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.2 | 10.24 | 11.32 | 332658 | 214699 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8BG | NP78BG | np7 8bg | np78bg | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 3236 | 1030 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.2 | 10.24 | 11.32 | 332710 | 215109 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8BH | NP78BH | np7 8bh | np78bh | Monmouthshire | Sir Fynwy | Llanvapley STW | 2869 | 1014 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.9 | 10.08 | 11.14 | 333603 | 215444 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8BL | NP78BL | np7 8bl | np78bl | Monmouthshire | Sir Fynwy | Llanvapley STW | 1957 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 334725 | 215387 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8BN | NP78BN | np7 8bn | np78bn | Monmouthshire | Sir Fynwy | Llanvapley STW | 1838 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 334707 | 215202 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8BP | NP78BP | np7 8bp | np78bp | Monmouthshire | Sir Fynwy | Llanvapley STW | 1364 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 334846 | 214588 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8BS | NP78BS | np7 8bs | np78bs | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 1926 | 1025 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.1 | 10.19 | 11.26 | 333568 | 214051 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8BT | NP78BT | np7 8bt | np78bt | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 2579 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 332948 | 214280 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8BW | NP78BW | np7 8bw | np78bw | Monmouthshire | Sir Fynwy | Llanvapley STW | 1552 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 334992 | 215083 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8DA | NP78DA | np7 8da | np78da | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1720 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 331466 | 219903 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8DB | NP78DB | np7 8db | np78db | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1652 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 332596 | 220734 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8DD | NP78DD | np7 8dd | np78dd | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1422 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 332370 | 220807 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8DG | NP78DG | np7 8dg | np78dg | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1760 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 332769 | 220823 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8DH | NP78DH | np7 8dh | np78dh | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1740 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 332581 | 220555 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8DJ | NP78DJ | np7 8dj | np78dj | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1753 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 332793 | 220891 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8DL | NP78DL | np7 8dl | np78dl | Monmouthshire | Sir Fynwy | Pandy STW | 1569 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 333201 | 221306 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8DN | NP78DN | np7 8dn | np78dn | Monmouthshire | Sir Fynwy | Pandy STW | 1094 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333347 | 221762 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8DP | NP78DP | np7 8dp | np78dp | Monmouthshire | Sir Fynwy | Pandy STW | 572 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333467 | 222272 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8DQ | NP78DQ | np7 8dq | np78dq | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1728 | 1094 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.39 | 10.87 | 12.02 | 332497 | 220470 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8DR | NP78DR | np7 8dr | np78dr | Monmouthshire | Sir Fynwy | Pandy STW | 531 | 994 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.53 | 9.88 | 10.92 | 334035 | 222962 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8DS | NP78DS | np7 8ds | np78ds | Monmouthshire | Sir Fynwy | Pandy STW | 415 | 1026 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.12 | 10.2 | 11.27 | 333573 | 222431 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8DT | NP78DT | np7 8dt | np78dt | Monmouthshire | Sir Fynwy | Pandy STW | 498 | 1026 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.12 | 10.2 | 11.27 | 333541 | 222345 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8DU | NP78DU | np7 8du | np78du | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1684 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 332652 | 220766 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8DW | NP78DW | np7 8dw | np78dw | Monmouthshire | Sir Fynwy | Pandy STW | 853 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 333361 | 222004 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8DX | NP78DX | np7 8dx | np78dx | Monmouthshire | Sir Fynwy | Cwmyoy STW | 1743 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 332643 | 220639 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8EA | NP78EA | np7 8ea | np78ea | Monmouthshire | Sir Fynwy | Pandy STW | 659 | 1026 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.12 | 10.2 | 11.27 | 333852 | 222274 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8ED | NP78ED | np7 8ed | np78ed | Monmouthshire | Sir Fynwy | Pandy STW | 1574 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 334886 | 222065 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8EE | NP78EE | np7 8ee | np78ee | Monmouthshire | Sir Fynwy | Pandy STW | 2497 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 335988 | 222484 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8EF | NP78EF | np7 8ef | np78ef | Monmouthshire | Sir Fynwy | Pandy STW | 2663 | 992 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.49 | 9.86 | 10.9 | 335666 | 221269 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8EG | NP78EG | np7 8eg | np78eg | Monmouthshire | Sir Fynwy | Pandy STW | 2208 | 1035 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.29 | 10.29 | 11.37 | 334791 | 221039 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8EH | NP78EH | np7 8eh | np78eh | Monmouthshire | Sir Fynwy | Pandy STW | 3045 | 1012 | 900to1200 | 2.03 | 1.48 | 1.09 | 18.86 | 10.06 | 11.12 | 334698 | 220036 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8EL | NP78EL | np7 8el | np78el | Monmouthshire | Sir Fynwy | Pandy STW | 4070 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 334270 | 218843 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8EN | NP78EN | np7 8en | np78en | Monmouthshire | Sir Fynwy | Cwmyoy STW | 3279 | 1087 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.26 | 10.81 | 11.94 | 333361 | 219144 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8EP | NP78EP | np7 8ep | np78ep | Monmouthshire | Sir Fynwy | Grosmont WwTW | 547 | 920 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.15 | 9.15 | 10.11 | 340391 | 224456 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8EQ | NP78EQ | np7 8eq | np78eq | Monmouthshire | Sir Fynwy | Grosmont WwTW | 625 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 340337 | 224528 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8ER | NP78ER | np7 8er | np78er | Monmouthshire | Sir Fynwy | Grosmont WwTW | 681 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 340450 | 224770 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8ES | NP78ES | np7 8es | np78es | Monmouthshire | Sir Fynwy | Grosmont WwTW | 696 | 886 | 700to900 | 1.77 | 1.3 | 0.95 | 16.51 | 8.81 | 9.73 | 340731 | 224935 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8ET | NP78ET | np7 8et | np78et | Monmouthshire | Sir Fynwy | Grosmont WwTW | 772 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 340261 | 224692 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8EW | NP78EW | np7 8ew | np78ew | Monmouthshire | Sir Fynwy | Pandy STW | 2447 | 1047 | 900to1200 | 2.1 | 1.53 | 1.12 | 19.51 | 10.41 | 11.5 | 334443 | 220578 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8EX | NP78EX | np7 8ex | np78ex | Monmouthshire | Sir Fynwy | Grosmont WwTW | 679 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 340297 | 224570 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8EY | NP78EY | np7 8ey | np78ey | Monmouthshire | Sir Fynwy | Grosmont WwTW | 1276 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 339756 | 224821 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HA | NP78HA | np7 8ha | np78ha | Monmouthshire | Sir Fynwy | Grosmont WwTW | 1535 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 339635 | 225127 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HB | NP78HB | np7 8hb | np78hb | Monmouthshire | Sir Fynwy | Grosmont WwTW | 2625 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 339347 | 226374 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HD | NP78HD | np7 8hd | np78hd | Monmouthshire | Sir Fynwy | Grosmont WwTW | 2457 | 911 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.98 | 9.06 | 10.01 | 339338 | 226155 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HE | NP78HE | np7 8he | np78he | Monmouthshire | Sir Fynwy | Grosmont WwTW | 2487 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 338660 | 225336 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HF | NP78HF | np7 8hf | np78hf | Monmouthshire | Sir Fynwy | Grosmont WwTW | 3005 | 952 | 900to1200 | 1.91 | 1.39 | 1.02 | 17.74 | 9.46 | 10.46 | 337993 | 225013 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HG | NP78HG | np7 8hg | np78hg | Monmouthshire | Sir Fynwy | Grosmont WwTW | 3702 | 952 | 900to1200 | 1.91 | 1.39 | 1.02 | 17.74 | 9.46 | 10.46 | 337213 | 224570 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HL | NP78HL | np7 8hl | np78hl | Monmouthshire | Sir Fynwy | Grosmont WwTW | 2513 | 957 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.84 | 9.51 | 10.51 | 338394 | 224096 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HN | NP78HN | np7 8hn | np78hn | Monmouthshire | Sir Fynwy | Grosmont WwTW | 3831 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 337422 | 222660 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HP | NP78HP | np7 8hp | np78hp | Monmouthshire | Sir Fynwy | Grosmont WwTW | 578 | 920 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.15 | 9.15 | 10.11 | 340355 | 224070 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HR | NP78HR | np7 8hr | np78hr | Monmouthshire | Sir Fynwy | Grosmont WwTW | 1227 | 920 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.15 | 9.15 | 10.11 | 339921 | 223522 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HS | NP78HS | np7 8hs | np78hs | Monmouthshire | Sir Fynwy | Grosmont WwTW | 1900 | 970 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.08 | 9.64 | 10.66 | 339205 | 223404 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HT | NP78HT | np7 8ht | np78ht | Monmouthshire | Sir Fynwy | Grosmont WwTW | 2728 | 975 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.17 | 9.69 | 10.71 | 338967 | 222337 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HU | NP78HU | np7 8hu | np78hu | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 3021 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 338220 | 221990 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8HW | NP78HW | np7 8hw | np78hw | Monmouthshire | Sir Fynwy | Pandy STW | 2150 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 333442 | 220694 | Brecon Beacons National Park LPA | SO | River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
NP7 8HY | NP78HY | np7 8hy | np78hy | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 1935 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 338848 | 220974 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LA | NP78LA | np7 8la | np78la | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 1746 | 971 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.1 | 9.65 | 10.67 | 338827 | 220184 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LB | NP78LB | np7 8lb | np78lb | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 1795 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 339163 | 221206 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LD | NP78LD | np7 8ld | np78ld | Monmouthshire | Sir Fynwy | Grosmont WwTW | 1938 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 340113 | 222490 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LE | NP78LE | np7 8le | np78le | Monmouthshire | Sir Fynwy | Grosmont WwTW | 1240 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 342094 | 223922 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LF | NP78LF | np7 8lf | np78lf | Monmouthshire | Sir Fynwy | Grosmont WwTW | 1538 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 342183 | 223412 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LG | NP78LG | np7 8lg | np78lg | Monmouthshire | Sir Fynwy | Grosmont WwTW | 2688 | 892 | 700to900 | 1.79 | 1.31 | 0.96 | 16.63 | 8.87 | 9.8 | 343077 | 222684 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LH | NP78LH | np7 8lh | np78lh | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 3821 | 886 | 700to900 | 1.77 | 1.3 | 0.95 | 16.51 | 8.81 | 9.73 | 343940 | 221891 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LL | NP78LL | np7 8ll | np78ll | Monmouthshire | Sir Fynwy | Grosmont WwTW | 909 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 341512 | 223587 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LN | NP78LN | np7 8ln | np78ln | Monmouthshire | Sir Fynwy | Grosmont WwTW | 175 | 904 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.85 | 8.99 | 9.93 | 340896 | 224085 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LP | NP78LP | np7 8lp | np78lp | Monmouthshire | Sir Fynwy | Grosmont WwTW | 599 | 920 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.15 | 9.15 | 10.11 | 340324 | 224421 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LQ | NP78LQ | np7 8lq | np78lq | Monmouthshire | Sir Fynwy | Grosmont WwTW | 640 | 920 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.15 | 9.15 | 10.11 | 340270 | 224363 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LR | NP78LR | np7 8lr | np78lr | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 2852 | 893 | 700to900 | 1.79 | 1.31 | 0.96 | 16.64 | 8.88 | 9.81 | 342876 | 221769 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LS | NP78LS | np7 8ls | np78ls | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 1653 | 937 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.46 | 9.31 | 10.29 | 342044 | 220839 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LT | NP78LT | np7 8lt | np78lt | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 1059 | 993 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.51 | 9.87 | 10.91 | 341388 | 220765 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LU | NP78LU | np7 8lu | np78lu | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 1356 | 920 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.15 | 9.15 | 10.11 | 341915 | 220264 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LW | NP78LW | np7 8lw | np78lw | Monmouthshire | Sir Fynwy | Grosmont WwTW | 366 | 904 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.85 | 8.99 | 9.93 | 340535 | 224255 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8LY | NP78LY | np7 8ly | np78ly | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 1308 | 920 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.15 | 9.15 | 10.11 | 341820 | 219709 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NA | NP78NA | np7 8na | np78na | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 1621 | 988 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.41 | 9.82 | 10.86 | 341162 | 221601 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8ND | NP78ND | np7 8nd | np78nd | Monmouthshire | Sir Fynwy | Grosmont WwTW | 907 | 944 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.59 | 9.38 | 10.37 | 340780 | 223361 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NE | NP78NE | np7 8ne | np78ne | Monmouthshire | Sir Fynwy | Grosmont WwTW | 351 | 904 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.85 | 8.99 | 9.93 | 340619 | 224052 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NL | NP78NL | np7 8nl | np78nl | Monmouthshire | Sir Fynwy | Llanvapley STW | 3570 | 995 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.55 | 9.89 | 10.93 | 335305 | 217439 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NN | NP78NN | np7 8nn | np78nn | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 3637 | 982 | 900to1200 | 1.97 | 1.44 | 1.05 | 18.3 | 9.76 | 10.79 | 337096 | 219022 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NP | NP78NP | np7 8np | np78np | Monmouthshire | Sir Fynwy | Pandy STW | 4195 | 974 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.15 | 9.68 | 10.7 | 336159 | 219585 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NR | NP78NR | np7 8nr | np78nr | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 3673 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 337012 | 221001 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NS | NP78NS | np7 8ns | np78ns | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 3121 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 337450 | 220087 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NT | NP78NT | np7 8nt | np78nt | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 2730 | 996 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.56 | 9.9 | 10.94 | 337883 | 220569 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NU | NP78NU | np7 8nu | np78nu | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 2158 | 981 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.28 | 9.75 | 10.78 | 338437 | 219769 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NW | NP78NW | np7 8nw | np78nw | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 3916 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 336663 | 219841 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8NY | NP78NY | np7 8ny | np78ny | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 2468 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 338306 | 219113 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PA | NP78PA | np7 8pa | np78pa | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 2089 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 338732 | 219101 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PB | NP78PB | np7 8pb | np78pb | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 1115 | 952 | 900to1200 | 1.91 | 1.39 | 1.02 | 17.74 | 9.46 | 10.46 | 339808 | 219279 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PD | NP78PD | np7 8pd | np78pd | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 668 | 972 | 900to1200 | 1.95 | 1.42 | 1.04 | 18.12 | 9.66 | 10.68 | 339932 | 219897 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PE | NP78PE | np7 8pe | np78pe | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 583 | 972 | 900to1200 | 1.95 | 1.42 | 1.04 | 18.12 | 9.66 | 10.68 | 340057 | 220370 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PF | NP78PF | np7 8pf | np78pf | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 121 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 340571 | 220214 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PG | NP78PG | np7 8pg | np78pg | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 183 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 340654 | 220256 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PH | NP78PH | np7 8ph | np78ph | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 128 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 340667 | 220177 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PL | NP78PL | np7 8pl | np78pl | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 230 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 340610 | 219867 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PN | NP78PN | np7 8pn | np78pn | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 342 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 340693 | 219774 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PP | NP78PP | np7 8pp | np78pp | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 639 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 340553 | 219454 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PR | NP78PR | np7 8pr | np78pr | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 892 | 952 | 900to1200 | 1.91 | 1.39 | 1.02 | 17.74 | 9.46 | 10.46 | 340068 | 219356 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PS | NP78PS | np7 8ps | np78ps | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 1079 | 952 | 900to1200 | 1.91 | 1.39 | 1.02 | 17.74 | 9.46 | 10.46 | 339933 | 219223 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PT | NP78PT | np7 8pt | np78pt | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 1587 | 952 | 900to1200 | 1.91 | 1.39 | 1.02 | 17.74 | 9.46 | 10.46 | 340494 | 218508 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PU | NP78PU | np7 8pu | np78pu | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 2109 | 938 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.48 | 9.32 | 10.31 | 339293 | 218415 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PW | NP78PW | np7 8pw | np78pw | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 1801 | 920 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.15 | 9.15 | 10.11 | 341193 | 218404 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8PY | NP78PY | np7 8py | np78py | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 3047 | 953 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.76 | 9.47 | 10.47 | 338226 | 218148 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RA | NP78RA | np7 8ra | np78ra | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 3458 | 953 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.76 | 9.47 | 10.47 | 337958 | 217829 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RB | NP78RB | np7 8rb | np78rb | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 3112 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 337626 | 219088 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RD | NP78RD | np7 8rd | np78rd | Monmouthshire | Sir Fynwy | Llanvapley STW | 3722 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 336890 | 217574 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RE | NP78RE | np7 8re | np78re | Monmouthshire | Sir Fynwy | Llanvapley STW | 3909 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 337012 | 217737 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RF | NP78RF | np7 8rf | np78rf | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 4289 | 982 | 900to1200 | 1.97 | 1.44 | 1.05 | 18.3 | 9.76 | 10.79 | 336543 | 218622 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RG | NP78RG | np7 8rg | np78rg | Monmouthshire | Sir Fynwy | Llanvapley STW | 3312 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 336286 | 217251 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RH | NP78RH | np7 8rh | np78rh | Monmouthshire | Sir Fynwy | Llanvapley STW | 2974 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 336110 | 216921 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RL | NP78RL | np7 8rl | np78rl | Monmouthshire | Sir Fynwy | Llanvapley STW | 2747 | 973 | 900to1200 | 1.95 | 1.42 | 1.04 | 18.14 | 9.67 | 10.69 | 337227 | 216431 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RN | NP78RN | np7 8rn | np78rn | Monmouthshire | Sir Fynwy | Llanvapley STW | 3807 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 336002 | 217754 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RP | NP78RP | np7 8rp | np78rp | Monmouthshire | Sir Fynwy | Llanvapley STW | 4356 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 335375 | 218251 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RR | NP78RR | np7 8rr | np78rr | Monmouthshire | Sir Fynwy | Pandy STW | 3913 | 974 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.15 | 9.68 | 10.7 | 336286 | 220078 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RS | NP78RS | np7 8rs | np78rs | Monmouthshire | Sir Fynwy | Pandy STW | 1439 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 333429 | 221406 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RT | NP78RT | np7 8rt | np78rt | Monmouthshire | Sir Fynwy | Pandy STW | 1565 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 333425 | 221280 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RU | NP78RU | np7 8ru | np78ru | Monmouthshire | Sir Fynwy | Pandy STW | 1455 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 333348 | 221397 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8RW | NP78RW | np7 8rw | np78rw | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 4753 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 336021 | 218721 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SA | NP78SA | np7 8sa | np78sa | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 1388 | 1025 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.1 | 10.19 | 11.26 | 334367 | 214166 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SB | NP78SB | np7 8sb | np78sb | Monmouthshire | Sir Fynwy | Llanvapley STW | 1333 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 334801 | 214412 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SD | NP78SD | np7 8sd | np78sd | Monmouthshire | Sir Fynwy | Llanvapley STW | 1088 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 335019 | 214291 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SE | NP78SE | np7 8se | np78se | Monmouthshire | Sir Fynwy | Llanvapley STW | 881 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 335332 | 214457 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SF | NP78SF | np7 8sf | np78sf | Monmouthshire | Sir Fynwy | Llanvapley STW | 727 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 335950 | 214669 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SG | NP78SG | np7 8sg | np78sg | Monmouthshire | Sir Fynwy | Llanvapley STW | 307 | 1005 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.73 | 9.99 | 11.04 | 336337 | 213839 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SH | NP78SH | np7 8sh | np78sh | Monmouthshire | Sir Fynwy | Llanvapley STW | 510 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 336555 | 214026 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SL | NP78SL | np7 8sl | np78sl | Monmouthshire | Sir Fynwy | Llanvapley STW | 571 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 336593 | 214127 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SN | NP78SN | np7 8sn | np78sn | Monmouthshire | Sir Fynwy | Llanvapley STW | 604 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 336648 | 214042 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SP | NP78SP | np7 8sp | np78sp | Monmouthshire | Sir Fynwy | Llanvapley STW | 1825 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 335822 | 215759 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SR | NP78SR | np7 8sr | np78sr | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 1654 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 338117 | 214187 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SS | NP78SS | np7 8ss | np78ss | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 1472 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 338767 | 213438 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8ST | NP78ST | np7 8st | np78st | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 932 | 960 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.89 | 9.54 | 10.55 | 338807 | 214422 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SU | NP78SU | np7 8su | np78su | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 214 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 339681 | 214758 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SW | NP78SW | np7 8sw | np78sw | Monmouthshire | Sir Fynwy | Llanvapley STW | 1166 | 976 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.19 | 9.7 | 10.72 | 336840 | 214807 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8SY | NP78SY | np7 8sy | np78sy | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 78 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 339745 | 214627 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8TA | NP78TA | np7 8ta | np78ta | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 1842 | 944 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.59 | 9.38 | 10.37 | 338165 | 215521 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8TB | NP78TB | np7 8tb | np78tb | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 732 | 944 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.59 | 9.38 | 10.37 | 339366 | 215185 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8TD | NP78TD | np7 8td | np78td | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 820 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 339716 | 215370 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8TE | NP78TE | np7 8te | np78te | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 1055 | 918 | 900to1200 | 1.84 | 1.34 | 0.99 | 17.11 | 9.13 | 10.09 | 340138 | 215522 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8TF | NP78TF | np7 8tf | np78tf | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 1029 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 340278 | 215421 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8TG | NP78TG | np7 8tg | np78tg | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 2119 | 917 | 900to1200 | 1.84 | 1.34 | 0.98 | 17.09 | 9.12 | 10.07 | 339689 | 216668 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8TH | NP78TH | np7 8th | np78th | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 2513 | 922 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.18 | 9.17 | 10.13 | 340678 | 216876 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8TL | NP78TL | np7 8tl | np78tl | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 1749 | 892 | 700to900 | 1.79 | 1.31 | 0.96 | 16.63 | 8.87 | 9.8 | 341355 | 215196 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8TN | NP78TN | np7 8tn | np78tn | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 689 | 937 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.46 | 9.31 | 10.29 | 340303 | 214167 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8UA | NP78UA | np7 8ua | np78ua | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 845 | 968 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.04 | 9.62 | 10.64 | 341330 | 219725 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8UB | NP78UB | np7 8ub | np78ub | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 3455 | 892 | 700to900 | 1.79 | 1.31 | 0.96 | 16.63 | 8.87 | 9.8 | 343962 | 220741 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8UD | NP78UD | np7 8ud | np78ud | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 2430 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 338295 | 216510 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8UE | NP78UE | np7 8ue | np78ue | Monmouthshire | Sir Fynwy | Llantilio Crosenny STW | 2876 | 935 | 900to1200 | 1.87 | 1.37 | 1 | 17.43 | 9.29 | 10.27 | 338962 | 217321 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8UF | NP78UF | np7 8uf | np78uf | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 2790 | 886 | 700to900 | 1.77 | 1.3 | 0.95 | 16.51 | 8.81 | 9.73 | 343355 | 219946 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8UG | NP78UG | np7 8ug | np78ug | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 4988 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 345550 | 220335 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8UH | NP78UH | np7 8uh | np78uh | Monmouthshire | Sir Fynwy | Great Craig Cross Ash STW | 4982 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 345540 | 220411 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 8UL | NP78UL | np7 8ul | np78ul | Monmouthshire | Sir Fynwy | Rockfield STW | 5493 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 346416 | 219839 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TH | NP79TH | np7 9th | np79th | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 908 | 1020 | 900to1200 | 2.04 | 1.49 | 1.1 | 19.01 | 10.14 | 11.21 | 334323 | 213115 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TL | NP79TL | np7 9tl | np79tl | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 2052 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 333275 | 213702 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TN | NP79TN | np7 9tn | np79tn | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 1735 | 1025 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.1 | 10.19 | 11.26 | 333747 | 213979 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TP | NP79TP | np7 9tp | np79tp | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 757 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 335006 | 213803 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TR | NP79TR | np7 9tr | np79tr | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 141 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 335097 | 213032 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TS | NP79TS | np7 9ts | np79ts | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 266 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 335040 | 212894 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TT | NP79TT | np7 9tt | np79tt | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 818 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 334862 | 212350 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TU | NP79TU | np7 9tu | np79tu | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 488 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 335403 | 212624 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TW | NP79TW | np7 9tw | np79tw | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 469 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 334852 | 213358 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9TY | NP79TY | np7 9ty | np79ty | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 874 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 335312 | 212210 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UA | NP79UA | np7 9ua | np79ua | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 1426 | 1032 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.23 | 10.26 | 11.34 | 336214 | 212048 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9UB | NP79UB | np7 9ub | np79ub | Monmouthshire | Sir Fynwy | Llanvapley STW | 1452 | 1010 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.82 | 10.04 | 11.1 | 337073 | 212919 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
NP7 9YH | NP79YH | np7 9yh | np79yh | Monmouthshire | Sir Fynwy | Llandewi Rhydderch STW | 260 | 1022 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.05 | 10.16 | 11.23 | 335197 | 212822 | Monmouthshire LPA | SO | River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council
SY16 4AY | SY164AY | sy16 4ay | sy164ay | Powys | Powys | Llanbadarn Ffynydd STW | 7029 | 1124 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.95 | 11.17 | 12.35 | 310893 | 284670 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY16 4BS | SY164BS | sy16 4bs | sy164bs | Powys | Powys | Llanbadarn Ffynydd STW | 5721 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 308540 | 283311 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6RN | SY186RN | sy18 6rn | sy186rn | Powys | Powys | Llangurig STW | 249 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 291017 | 279820 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6RP | SY186RP | sy18 6rp | sy186rp | Powys | Powys | Llangurig STW | 958 | 1628 | Over1500 | 3.26 | 2.38 | 1.75 | 30.34 | 16.18 | 17.89 | 290617 | 278685 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6RR | SY186RR | sy18 6rr | sy186rr | Powys | Powys | Llangurig STW | 718 | 1734 | Over1500 | 3.47 | 2.54 | 1.86 | 32.32 | 17.24 | 19.05 | 290329 | 280035 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6RS | SY186RS | sy18 6rs | sy186rs | Powys | Powys | Llangurig STW | 2245 | 1855 | Over1500 | 3.71 | 2.72 | 1.99 | 34.57 | 18.44 | 20.38 | 288683 | 279950 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6RT | SY186RT | sy18 6rt | sy186rt | Powys | Powys | Llangurig STW | 2399 | 1855 | Over1500 | 3.71 | 2.72 | 1.99 | 34.57 | 18.44 | 20.38 | 288673 | 280490 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6RU | SY186RU | sy18 6ru | sy186ru | Powys | Powys | Llangurig STW | 3838 | 2012 | Over1500 | 4.03 | 2.95 | 2.16 | 37.5 | 20 | 22.11 | 287427 | 281231 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6RW | SY186RW | sy18 6rw | sy186rw | Powys | Powys | Llangurig STW | 318 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 291064 | 279872 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6RX | SY186RX | sy18 6rx | sy186rx | Powys | Powys | Llangurig STW | 3513 | 1483 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.64 | 14.74 | 16.29 | 291905 | 276235 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6RY | SY186RY | sy18 6ry | sy186ry | Powys | Powys | Llangurig STW | 5557 | 1494 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.85 | 14.85 | 16.41 | 292006 | 274156 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6RZ | SY186RZ | sy18 6rz | sy186rz | Powys | Powys | Llangurig STW | 4701 | 1681 | Over1500 | 3.36 | 2.46 | 1.81 | 31.33 | 16.71 | 18.47 | 290942 | 274900 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SA | SY186SA | sy18 6sa | sy186sa | Powys | Powys | Llangurig STW | 3069 | 1687 | Over1500 | 3.38 | 2.47 | 1.81 | 31.44 | 16.77 | 18.53 | 291120 | 276540 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SB | SY186SB | sy18 6sb | sy186sb | Powys | Powys | Llangurig STW | 568 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 290935 | 280167 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SG | SY186SG | sy18 6sg | sy186sg | Powys | Powys | Llangurig STW | 316 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 290843 | 279911 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SH | SY186SH | sy18 6sh | sy186sh | Powys | Powys | Llangurig STW | 464 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 290939 | 280062 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SJ | SY186SJ | sy18 6sj | sy186sj | Powys | Powys | Llangurig STW | 1792 | 1634 | Over1500 | 3.27 | 2.39 | 1.75 | 30.46 | 16.24 | 17.95 | 292428 | 280536 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SL | SY186SL | sy18 6sl | sy186sl | Powys | Powys | Llangurig STW | 1213 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 291029 | 280806 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SN | SY186SN | sy18 6sn | sy186sn | Powys | Powys | Llangurig STW | 1352 | 1736 | Over1500 | 3.47 | 2.54 | 1.86 | 32.36 | 17.26 | 19.07 | 289959 | 280571 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SQ | SY186SQ | sy18 6sq | sy186sq | Powys | Powys | Llangurig STW | 376 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 290964 | 279970 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SU | SY186SU | sy18 6su | sy186su | Powys | Powys | Llangurig STW | 4875 | 2039 | Over1500 | 4.08 | 2.99 | 2.19 | 38 | 20.27 | 22.4 | 286533 | 281763 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SW | SY186SW | sy18 6sw | sy186sw | Powys | Powys | Llangurig STW | 2542 | 1796 | Over1500 | 3.59 | 2.63 | 1.93 | 33.47 | 17.85 | 19.73 | 288994 | 281281 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SX | SY186SX | sy18 6sx | sy186sx | Powys | Powys | Llangurig STW | 4013 | 1908 | Over1500 | 3.82 | 2.79 | 2.05 | 35.56 | 18.97 | 20.96 | 287733 | 282063 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SY | SY186SY | sy18 6sy | sy186sy | Powys | Powys | Llangurig STW | 7027 | 2232 | Over1500 | 4.47 | 3.27 | 2.4 | 41.6 | 22.19 | 24.52 | 284531 | 282564 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6SZ | SY186SZ | sy18 6sz | sy186sz | Powys | Powys | Llangurig STW | 3836 | 1908 | Over1500 | 3.82 | 2.79 | 2.05 | 35.56 | 18.97 | 20.96 | 287656 | 281645 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY18 6TA | SY186TA | sy18 6ta | sy186ta | Powys | Powys | Llangurig STW | 3889 | 2012 | Over1500 | 4.03 | 2.95 | 2.16 | 37.5 | 20 | 22.11 | 287206 | 280814 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
SY23 3LE | SY233LE | sy23 3le | sy233le | Ceredigion | Sir Ceredigion | Llangurig STW | 12019 | 2487 | Over1500 | 4.98 | 3.64 | 2.67 | 46.35 | 24.72 | 27.32 | 279759 | 284103 | Ceredigion LPA | CE | River Wye/ Afon Gwy | Cyngor Sir Ceredigion | Ceredigion County Council
SY23 4AQ | SY234AQ | sy23 4aq | sy234aq | Powys | Powys | Llangurig STW | 6132 | 2017 | Over1500 | 4.04 | 2.95 | 2.17 | 37.59 | 20.05 | 22.16 | 286822 | 275023 | Powys LPA | PO | River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council
CH6 5AB | CH65AB | ch6 5ab | ch65ab | Flintshire | Sir Y Fflint | Rhosesmor STW | 5486 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324016 | 372730 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AD | CH65AD | ch6 5ad | ch65ad | Flintshire | Sir Y Fflint | Rhosesmor STW | 5962 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324404 | 373042 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AE | CH65AE | ch6 5ae | ch65ae | Flintshire | Sir Y Fflint | Rhosesmor STW | 5952 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324355 | 373064 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AF | CH65AF | ch6 5af | ch65af | Flintshire | Sir Y Fflint | Rhosesmor STW | 5701 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324174 | 372883 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AG | CH65AG | ch6 5ag | ch65ag | Flintshire | Sir Y Fflint | Rhosesmor STW | 5947 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324342 | 373067 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AJ | CH65AJ | ch6 5aj | ch65aj | Flintshire | Sir Y Fflint | Rhosesmor STW | 5978 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324403 | 373063 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AL | CH65AL | ch6 5al | ch65al | Flintshire | Sir Y Fflint | Rhosesmor STW | 5966 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324361 | 373077 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AN | CH65AN | ch6 5an | ch65an | Flintshire | Sir Y Fflint | Rhosesmor STW | 5954 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324296 | 373106 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AP | CH65AP | ch6 5ap | ch65ap | Flintshire | Sir Y Fflint | Rhosesmor STW | 5837 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324253 | 372994 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AQ | CH65AQ | ch6 5aq | ch65aq | Flintshire | Sir Y Fflint | Rhosesmor STW | 5954 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324296 | 373106 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AS | CH65AS | ch6 5as | ch65as | Flintshire | Sir Y Fflint | Rhosesmor STW | 5694 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324222 | 372843 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AT | CH65AT | ch6 5at | ch65at | Flintshire | Sir Y Fflint | Rhosesmor STW | 5712 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324172 | 372898 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AW | CH65AW | ch6 5aw | ch65aw | Flintshire | Sir Y Fflint | Rhosesmor STW | 5954 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324296 | 373106 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AX | CH65AX | ch6 5ax | ch65ax | Flintshire | Sir Y Fflint | Rhosesmor STW | 6293 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324346 | 373477 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5AZ | CH65AZ | ch6 5az | ch65az | Flintshire | Sir Y Fflint | Rhosesmor STW | 5773 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324256 | 372915 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5BD | CH65BD | ch6 5bd | ch65bd | Flintshire | Sir Y Fflint | Rhosesmor STW | 5826 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324294 | 372953 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5BE | CH65BE | ch6 5be | ch65be | Flintshire | Sir Y Fflint | Rhosesmor STW | 5760 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324313 | 372859 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5BF | CH65BF | ch6 5bf | ch65bf | Flintshire | Sir Y Fflint | Connahs Quay STW | 3905 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 326713 | 371052 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5BG | CH65BG | ch6 5bg | ch65bg | Flintshire | Sir Y Fflint | Rhosesmor STW | 5738 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324159 | 372938 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5BL | CH65BL | ch6 5bl | ch65bl | Flintshire | Sir Y Fflint | Rhosesmor STW | 6047 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324543 | 373048 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5BN | CH65BN | ch6 5bn | ch65bn | Flintshire | Sir Y Fflint | Rhosesmor STW | 3545 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 323924 | 370152 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5BP | CH65BP | ch6 5bp | ch65bp | Flintshire | Sir Y Fflint | Rhosesmor STW | 5961 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324509 | 372966 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5BQ | CH65BQ | ch6 5bq | ch65bq | Flintshire | Sir Y Fflint | Rhosesmor STW | 5799 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324189 | 372991 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5BR | CH65BR | ch6 5br | ch65br | Flintshire | Sir Y Fflint | Rhosesmor STW | 6010 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324341 | 373143 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5BS | CH65BS | ch6 5bs | ch65bs | Flintshire | Sir Y Fflint | Rhosesmor STW | 6010 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324341 | 373143 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5BX | CH65BX | ch6 5bx | ch65bx | Flintshire | Sir Y Fflint | Rhosesmor STW | 5923 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324430 | 372977 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DD | CH65DD | ch6 5dd | ch65dd | Flintshire | Sir Y Fflint | Rhosesmor STW | 5991 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324605 | 372932 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DE | CH65DE | ch6 5de | ch65de | Flintshire | Sir Y Fflint | Rhosesmor STW | 5864 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324503 | 372850 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DF | CH65DF | ch6 5df | ch65df | Flintshire | Sir Y Fflint | Rhosesmor STW | 5960 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324580 | 372913 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DG | CH65DG | ch6 5dg | ch65dg | Flintshire | Sir Y Fflint | Rhosesmor STW | 5930 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324546 | 372900 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DH | CH65DH | ch6 5dh | ch65dh | Flintshire | Sir Y Fflint | Rhosesmor STW | 5991 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324609 | 372930 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DJ | CH65DJ | ch6 5dj | ch65dj | Flintshire | Sir Y Fflint | Rhosesmor STW | 5828 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324430 | 372859 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DL | CH65DL | ch6 5dl | ch65dl | Flintshire | Sir Y Fflint | Rhosesmor STW | 5763 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324467 | 372751 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DN | CH65DN | ch6 5dn | ch65dn | Flintshire | Sir Y Fflint | Rhosesmor STW | 5871 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324565 | 372812 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DP | CH65DP | ch6 5dp | ch65dp | Flintshire | Sir Y Fflint | Rhosesmor STW | 5671 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324392 | 372693 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DQ | CH65DQ | ch6 5dq | ch65dq | Flintshire | Sir Y Fflint | Rhosesmor STW | 5843 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324477 | 372844 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DR | CH65DR | ch6 5dr | ch65dr | Flintshire | Sir Y Fflint | Rhosesmor STW | 5867 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324667 | 372728 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DS | CH65DS | ch6 5ds | ch65ds | Flintshire | Sir Y Fflint | Rhosesmor STW | 5864 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324688 | 372707 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DT | CH65DT | ch6 5dt | ch65dt | Flintshire | Sir Y Fflint | Rhosesmor STW | 6017 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324798 | 372814 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DU | CH65DU | ch6 5du | ch65du | Flintshire | Sir Y Fflint | Rhosesmor STW | 6039 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324957 | 372710 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DW | CH65DW | ch6 5dw | ch65dw | Flintshire | Sir Y Fflint | Rhosesmor STW | 5882 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324595 | 372803 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DY | CH65DY | ch6 5dy | ch65dy | Flintshire | Sir Y Fflint | Connahs Quay STW | 6050 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 325119 | 372597 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5DZ | CH65DZ | ch6 5dz | ch65dz | Flintshire | Sir Y Fflint | Connahs Quay STW | 5938 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325186 | 372493 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EA | CH65EA | ch6 5ea | ch65ea | Flintshire | Sir Y Fflint | Connahs Quay STW | 5656 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325324 | 372174 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EB | CH65EB | ch6 5eb | ch65eb | Flintshire | Sir Y Fflint | Rhosesmor STW | 6065 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 325075 | 372639 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5ED | CH65ED | ch6 5ed | ch65ed | Flintshire | Sir Y Fflint | Connahs Quay STW | 5797 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325288 | 372391 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EE | CH65EE | ch6 5ee | ch65ee | Flintshire | Sir Y Fflint | Rhosesmor STW | 5886 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325064 | 372405 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EF | CH65EF | ch6 5ef | ch65ef | Flintshire | Sir Y Fflint | Rhosesmor STW | 5908 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325029 | 372468 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EG | CH65EG | ch6 5eg | ch65eg | Flintshire | Sir Y Fflint | Rhosesmor STW | 5907 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325106 | 372394 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EH | CH65EH | ch6 5eh | ch65eh | Flintshire | Sir Y Fflint | Connahs Quay STW | 6122 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 325139 | 372761 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EJ | CH65EJ | ch6 5ej | ch65ej | Flintshire | Sir Y Fflint | Rhosesmor STW | 5635 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324896 | 372218 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EL | CH65EL | ch6 5el | ch65el | Flintshire | Sir Y Fflint | Rhosesmor STW | 5677 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324968 | 372208 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EN | CH65EN | ch6 5en | ch65en | Flintshire | Sir Y Fflint | Connahs Quay STW | 5726 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325279 | 372235 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EP | CH65EP | ch6 5ep | ch65ep | Flintshire | Sir Y Fflint | Rhosesmor STW | 6147 | 776 | 700to900 | 1.55 | 1.14 | 0.83 | 14.46 | 7.71 | 8.53 | 324004 | 373511 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EQ | CH65EQ | ch6 5eq | ch65eq | Flintshire | Sir Y Fflint | Rhosesmor STW | 5887 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325111 | 372361 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5ER | CH65ER | ch6 5er | ch65er | Flintshire | Sir Y Fflint | Rhosesmor STW | 6008 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324300 | 373168 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5ES | CH65ES | ch6 5es | ch65es | Flintshire | Sir Y Fflint | Rhosesmor STW | 6113 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324354 | 373258 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5ET | CH65ET | ch6 5et | ch65et | Flintshire | Sir Y Fflint | Rhosesmor STW | 5110 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 323239 | 372742 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EU | CH65EU | ch6 5eu | ch65eu | Flintshire | Sir Y Fflint | Connahs Quay STW | 5631 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325448 | 372333 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EW | CH65EW | ch6 5ew | ch65ew | Flintshire | Sir Y Fflint | Connahs Quay STW | 5737 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325204 | 372125 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EX | CH65EX | ch6 5ex | ch65ex | Flintshire | Sir Y Fflint | Rhosesmor STW | 5826 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323798 | 373258 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EY | CH65EY | ch6 5ey | ch65ey | Flintshire | Sir Y Fflint | Rhosesmor STW | 5351 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323565 | 372844 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5EZ | CH65EZ | ch6 5ez | ch65ez | Flintshire | Sir Y Fflint | Rhosesmor STW | 5291 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 323472 | 372826 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FA | CH65FA | ch6 5fa | ch65fa | Flintshire | Sir Y Fflint | Rhosesmor STW | 5848 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324208 | 373037 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FB | CH65FB | ch6 5fb | ch65fb | Flintshire | Sir Y Fflint | Rhosesmor STW | 6081 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324485 | 373131 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FD | CH65FD | ch6 5fd | ch65fd | Flintshire | Sir Y Fflint | Rhosesmor STW | 5856 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324397 | 372918 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FE | CH65FE | ch6 5fe | ch65fe | Flintshire | Sir Y Fflint | Rhosesmor STW | 5904 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324387 | 372984 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FF | CH65FF | ch6 5ff | ch65ff | Flintshire | Sir Y Fflint | Rhosesmor STW | 5947 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324476 | 372973 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FG | CH65FG | ch6 5fg | ch65fg | Flintshire | Sir Y Fflint | Rhosesmor STW | 5799 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324372 | 372865 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FH | CH65FH | ch6 5fh | ch65fh | Flintshire | Sir Y Fflint | Rhosesmor STW | 5590 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325190 | 371848 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FJ | CH65FJ | ch6 5fj | ch65fj | Flintshire | Sir Y Fflint | Connahs Quay STW | 5597 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325226 | 371863 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FL | CH65FL | ch6 5fl | ch65fl | Flintshire | Sir Y Fflint | Connahs Quay STW | 5532 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325293 | 371852 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FN | CH65FN | ch6 5fn | ch65fn | Flintshire | Sir Y Fflint | Connahs Quay STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325337 | 371775 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FP | CH65FP | ch6 5fp | ch65fp | Flintshire | Sir Y Fflint | Connahs Quay STW | 5431 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325381 | 371803 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FQ | CH65FQ | ch6 5fq | ch65fq | Flintshire | Sir Y Fflint | Connahs Quay STW | 5507 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325321 | 371851 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FR | CH65FR | ch6 5fr | ch65fr | Flintshire | Sir Y Fflint | Connahs Quay STW | 5442 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325424 | 371910 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FS | CH65FS | ch6 5fs | ch65fs | Flintshire | Sir Y Fflint | Connahs Quay STW | 5436 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325408 | 371867 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FT | CH65FT | ch6 5ft | ch65ft | Flintshire | Sir Y Fflint | Connahs Quay STW | 5432 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325407 | 371856 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FW | CH65FW | ch6 5fw | ch65fw | Flintshire | Sir Y Fflint | Connahs Quay STW | 5664 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325216 | 371991 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FX | CH65FX | ch6 5fx | ch65fx | Flintshire | Sir Y Fflint | Connahs Quay STW | 5521 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325358 | 371955 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FY | CH65FY | ch6 5fy | ch65fy | Flintshire | Sir Y Fflint | Rhosesmor STW | 5673 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324919 | 372249 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5FZ | CH65FZ | ch6 5fz | ch65fz | Flintshire | Sir Y Fflint | Rhosesmor STW | 3623 | 801 | 700to900 | 1.6 | 1.17 | 0.86 | 14.93 | 7.96 | 8.8 | 323731 | 370529 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GA | CH65GA | ch6 5ga | ch65ga | Flintshire | Sir Y Fflint | Connahs Quay STW | 6001 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 325207 | 372644 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GB | CH65GB | ch6 5gb | ch65gb | Flintshire | Sir Y Fflint | Rhosesmor STW | 5958 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324109 | 373230 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GD | CH65GD | ch6 5gd | ch65gd | Flintshire | Sir Y Fflint | Rhosesmor STW | 6036 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324340 | 373175 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GE | CH65GE | ch6 5ge | ch65ge | Flintshire | Sir Y Fflint | Rhosesmor STW | 6053 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324510 | 373079 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GF | CH65GF | ch6 5gf | ch65gf | Flintshire | Sir Y Fflint | Rhosesmor STW | 5688 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325119 | 372070 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GG | CH65GG | ch6 5gg | ch65gg | Flintshire | Sir Y Fflint | Rhosesmor STW | 5621 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325045 | 372051 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GH | CH65GH | ch6 5gh | ch65gh | Flintshire | Sir Y Fflint | Rhosesmor STW | 5608 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325076 | 371999 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GJ | CH65GJ | ch6 5gj | ch65gj | Flintshire | Sir Y Fflint | Rhosesmor STW | 5731 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325125 | 372126 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GL | CH65GL | ch6 5gl | ch65gl | Flintshire | Sir Y Fflint | Rhosesmor STW | 5712 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325167 | 372054 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GN | CH65GN | ch6 5gn | ch65gn | Flintshire | Sir Y Fflint | Rhosesmor STW | 5709 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325181 | 372035 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GP | CH65GP | ch6 5gp | ch65gp | Flintshire | Sir Y Fflint | Connahs Quay STW | 5654 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325250 | 372035 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GQ | CH65GQ | ch6 5gq | ch65gq | Flintshire | Sir Y Fflint | Rhosesmor STW | 5977 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324266 | 373153 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GR | CH65GR | ch6 5gr | ch65gr | Flintshire | Sir Y Fflint | Rhosesmor STW | 5957 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324516 | 372956 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GW | CH65GW | ch6 5gw | ch65gw | Flintshire | Sir Y Fflint | Rhosesmor STW | 4799 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323880 | 371987 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GY | CH65GY | ch6 5gy | ch65gy | Flintshire | Sir Y Fflint | Rhosesmor STW | 5596 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324878 | 372182 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GZ | CH65GZ | ch6 5gz | ch65gz | Flintshire | Sir Y Fflint | Rhosesmor STW | 5155 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323690 | 372545 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HA | CH65HA | ch6 5ha | ch65ha | Flintshire | Sir Y Fflint | Connahs Quay STW | 5599 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325345 | 372095 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HB | CH65HB | ch6 5hb | ch65hb | Flintshire | Sir Y Fflint | Rhosesmor STW | 5654 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324112 | 372868 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HD | CH65HD | ch6 5hd | ch65hd | Flintshire | Sir Y Fflint | Rhosesmor STW | 5262 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 323487 | 372785 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HE | CH65HE | ch6 5he | ch65he | Flintshire | Sir Y Fflint | Rhosesmor STW | 5231 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323546 | 372718 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HF | CH65HF | ch6 5hf | ch65hf | Flintshire | Sir Y Fflint | Rhosesmor STW | 5229 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323576 | 372698 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HG | CH65HG | ch6 5hg | ch65hg | Flintshire | Sir Y Fflint | Rhosesmor STW | 5370 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323860 | 372693 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HH | CH65HH | ch6 5hh | ch65hh | Flintshire | Sir Y Fflint | Rhosesmor STW | 5327 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323911 | 372609 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HJ | CH65HJ | ch6 5hj | ch65hj | Flintshire | Sir Y Fflint | Rhosesmor STW | 5219 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323687 | 372622 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HL | CH65HL | ch6 5hl | ch65hl | Flintshire | Sir Y Fflint | Rhosesmor STW | 5229 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323659 | 372651 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HN | CH65HN | ch6 5hn | ch65hn | Flintshire | Sir Y Fflint | Rhosesmor STW | 5166 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323750 | 372521 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HP | CH65HP | ch6 5hp | ch65hp | Flintshire | Sir Y Fflint | Rhosesmor STW | 5200 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323828 | 372512 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HQ | CH65HQ | ch6 5hq | ch65hq | Flintshire | Sir Y Fflint | Rhosesmor STW | 5310 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323831 | 372640 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HR | CH65HR | ch6 5hr | ch65hr | Flintshire | Sir Y Fflint | Rhosesmor STW | 5172 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323858 | 372459 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HS | CH65HS | ch6 5hs | ch65hs | Flintshire | Sir Y Fflint | Rhosesmor STW | 5256 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323851 | 372564 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HT | CH65HT | ch6 5ht | ch65ht | Flintshire | Sir Y Fflint | Rhosesmor STW | 5165 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323911 | 372415 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HU | CH65HU | ch6 5hu | ch65hu | Flintshire | Sir Y Fflint | Rhosesmor STW | 5172 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324016 | 372349 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HW | CH65HW | ch6 5hw | ch65hw | Flintshire | Sir Y Fflint | Rhosesmor STW | 5200 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323748 | 372562 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HX | CH65HX | ch6 5hx | ch65hx | Flintshire | Sir Y Fflint | Rhosesmor STW | 5548 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324055 | 372779 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HY | CH65HY | ch6 5hy | ch65hy | Flintshire | Sir Y Fflint | Rhosesmor STW | 5581 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324121 | 372775 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5HZ | CH65HZ | ch6 5hz | ch65hz | Flintshire | Sir Y Fflint | Rhosesmor STW | 5446 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324065 | 372650 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JB | CH65JB | ch6 5jb | ch65jb | Flintshire | Sir Y Fflint | Rhosesmor STW | 5657 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325002 | 372145 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JD | CH65JD | ch6 5jd | ch65jd | Flintshire | Sir Y Fflint | Rhosesmor STW | 5866 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324738 | 372668 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JE | CH65JE | ch6 5je | ch65je | Flintshire | Sir Y Fflint | Rhosesmor STW | 5630 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324600 | 372476 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JF | CH65JF | ch6 5jf | ch65jf | Flintshire | Sir Y Fflint | Rhosesmor STW | 5640 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324645 | 372451 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JG | CH65JG | ch6 5jg | ch65jg | Flintshire | Sir Y Fflint | Rhosesmor STW | 5877 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324818 | 372616 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JH | CH65JH | ch6 5jh | ch65jh | Flintshire | Sir Y Fflint | Rhosesmor STW | 5842 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324828 | 372560 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JJ | CH65JJ | ch6 5jj | ch65jj | Flintshire | Sir Y Fflint | Rhosesmor STW | 5427 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324127 | 372584 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JL | CH65JL | ch6 5jl | ch65jl | Flintshire | Sir Y Fflint | Rhosesmor STW | 5681 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325030 | 372152 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JN | CH65JN | ch6 5jn | ch65jn | Flintshire | Sir Y Fflint | Rhosesmor STW | 5885 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324922 | 372535 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JP | CH65JP | ch6 5jp | ch65jp | Flintshire | Sir Y Fflint | Rhosesmor STW | 5643 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324728 | 372384 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JQ | CH65JQ | ch6 5jq | ch65jq | Flintshire | Sir Y Fflint | Rhosesmor STW | 5640 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324674 | 372427 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JR | CH65JR | ch6 5jr | ch65jr | Flintshire | Sir Y Fflint | Rhosesmor STW | 5889 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324946 | 372519 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JS | CH65JS | ch6 5js | ch65js | Flintshire | Sir Y Fflint | Rhosesmor STW | 5895 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324972 | 372503 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JT | CH65JT | ch6 5jt | ch65jt | Flintshire | Sir Y Fflint | Rhosesmor STW | 5715 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324670 | 372528 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JU | CH65JU | ch6 5ju | ch65ju | Flintshire | Sir Y Fflint | Rhosesmor STW | 5728 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324911 | 372332 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JW | CH65JW | ch6 5jw | ch65jw | Flintshire | Sir Y Fflint | Rhosesmor STW | 5871 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324887 | 372548 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JX | CH65JX | ch6 5jx | ch65jx | Flintshire | Sir Y Fflint | Rhosesmor STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324648 | 372209 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JY | CH65JY | ch6 5jy | ch65jy | Flintshire | Sir Y Fflint | Rhosesmor STW | 5519 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324628 | 372306 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5JZ | CH65JZ | ch6 5jz | ch65jz | Flintshire | Sir Y Fflint | Rhosesmor STW | 5536 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324735 | 372234 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LA | CH65LA | ch6 5la | ch65la | Flintshire | Sir Y Fflint | Rhosesmor STW | 5989 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324410 | 373071 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LG | CH65LG | ch6 5lg | ch65lg | Flintshire | Sir Y Fflint | Rhosesmor STW | 5236 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324132 | 372344 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LH | CH65LH | ch6 5lh | ch65lh | Flintshire | Sir Y Fflint | Rhosesmor STW | 5058 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324132 | 372120 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LJ | CH65LJ | ch6 5lj | ch65lj | Flintshire | Sir Y Fflint | Rhosesmor STW | 5179 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324180 | 372236 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LL | CH65LL | ch6 5ll | ch65ll | Flintshire | Sir Y Fflint | Rhosesmor STW | 4993 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324234 | 371952 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LN | CH65LN | ch6 5ln | ch65ln | Flintshire | Sir Y Fflint | Rhosesmor STW | 5078 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324227 | 372069 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LP | CH65LP | ch6 5lp | ch65lp | Flintshire | Sir Y Fflint | Rhosesmor STW | 5208 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324240 | 372225 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LQ | CH65LQ | ch6 5lq | ch65lq | Flintshire | Sir Y Fflint | Rhosesmor STW | 5339 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324117 | 372483 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LR | CH65LR | ch6 5lr | ch65lr | Flintshire | Sir Y Fflint | Rhosesmor STW | 5197 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324208 | 372237 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LS | CH65LS | ch6 5ls | ch65ls | Flintshire | Sir Y Fflint | Rhosesmor STW | 5300 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324276 | 372314 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LT | CH65LT | ch6 5lt | ch65lt | Flintshire | Sir Y Fflint | Rhosesmor STW | 5214 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324304 | 372181 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LU | CH65LU | ch6 5lu | ch65lu | Flintshire | Sir Y Fflint | Rhosesmor STW | 5224 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324335 | 372169 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LW | CH65LW | ch6 5lw | ch65lw | Flintshire | Sir Y Fflint | Rhosesmor STW | 5132 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324348 | 372037 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LX | CH65LX | ch6 5lx | ch65lx | Flintshire | Sir Y Fflint | Rhosesmor STW | 5250 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324367 | 372176 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LY | CH65LY | ch6 5ly | ch65ly | Flintshire | Sir Y Fflint | Rhosesmor STW | 5209 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324617 | 371896 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5LZ | CH65LZ | ch6 5lz | ch65lz | Flintshire | Sir Y Fflint | Rhosesmor STW | 4979 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324443 | 371744 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NA | CH65NA | ch6 5na | ch65na | Flintshire | Sir Y Fflint | Rhosesmor STW | 5844 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324343 | 372941 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NB | CH65NB | ch6 5nb | ch65nb | Flintshire | Sir Y Fflint | Rhosesmor STW | 5241 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324390 | 372145 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5ND | CH65ND | ch6 5nd | ch65nd | Flintshire | Sir Y Fflint | Rhosesmor STW | 5234 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324410 | 372118 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NE | CH65NE | ch6 5ne | ch65ne | Flintshire | Sir Y Fflint | Rhosesmor STW | 5320 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324268 | 372346 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NF | CH65NF | ch6 5nf | ch65nf | Flintshire | Sir Y Fflint | Rhosesmor STW | 5493 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324303 | 372537 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NG | CH65NG | ch6 5ng | ch65ng | Flintshire | Sir Y Fflint | Rhosesmor STW | 5844 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324343 | 372941 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NH | CH65NH | ch6 5nh | ch65nh | Flintshire | Sir Y Fflint | Rhosesmor STW | 5418 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324253 | 372481 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NN | CH65NN | ch6 5nn | ch65nn | Flintshire | Sir Y Fflint | Rhosesmor STW | 6062 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324478 | 373112 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NP | CH65NP | ch6 5np | ch65np | Flintshire | Sir Y Fflint | Connahs Quay STW | 5549 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325423 | 372131 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NR | CH65NR | ch6 5nr | ch65nr | Flintshire | Sir Y Fflint | Rhosesmor STW | 6009 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324491 | 373039 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NS | CH65NS | ch6 5ns | ch65ns | Flintshire | Sir Y Fflint | Rhosesmor STW | 6098 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324397 | 373212 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NT | CH65NT | ch6 5nt | ch65nt | Flintshire | Sir Y Fflint | Rhosesmor STW | 6196 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324469 | 373282 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NU | CH65NU | ch6 5nu | ch65nu | Flintshire | Sir Y Fflint | Rhosesmor STW | 6233 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324517 | 373294 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NW | CH65NW | ch6 5nw | ch65nw | Flintshire | Sir Y Fflint | Rhosesmor STW | 6077 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324480 | 373129 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NX | CH65NX | ch6 5nx | ch65nx | Flintshire | Sir Y Fflint | Rhosesmor STW | 6199 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324540 | 373236 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NY | CH65NY | ch6 5ny | ch65ny | Flintshire | Sir Y Fflint | Rhosesmor STW | 5574 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324219 | 372698 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5NZ | CH65NZ | ch6 5nz | ch65nz | Flintshire | Sir Y Fflint | Rhosesmor STW | 4824 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 324873 | 371023 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PA | CH65PA | ch6 5pa | ch65pa | Flintshire | Sir Y Fflint | Rhosesmor STW | 5268 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324696 | 371901 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PB | CH65PB | ch6 5pb | ch65pb | Flintshire | Sir Y Fflint | Rhosesmor STW | 5299 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324724 | 371917 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PD | CH65PD | ch6 5pd | ch65pd | Flintshire | Sir Y Fflint | Rhosesmor STW | 6248 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324533 | 373301 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PE | CH65PE | ch6 5pe | ch65pe | Flintshire | Sir Y Fflint | Rhosesmor STW | 6238 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324632 | 373219 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PF | CH65PF | ch6 5pf | ch65pf | Flintshire | Sir Y Fflint | Rhosesmor STW | 6185 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324577 | 373193 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PG | CH65PG | ch6 5pg | ch65pg | Flintshire | Sir Y Fflint | Rhosesmor STW | 6149 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324557 | 373163 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PH | CH65PH | ch6 5ph | ch65ph | Flintshire | Sir Y Fflint | Rhosesmor STW | 6210 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324706 | 373131 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PJ | CH65PJ | ch6 5pj | ch65pj | Flintshire | Sir Y Fflint | Rhosesmor STW | 6238 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324793 | 373100 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PL | CH65PL | ch6 5pl | ch65pl | Flintshire | Sir Y Fflint | Rhosesmor STW | 5263 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324736 | 371854 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PN | CH65PN | ch6 5pn | ch65pn | Flintshire | Sir Y Fflint | Rhosesmor STW | 5175 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324764 | 371699 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PP | CH65PP | ch6 5pp | ch65pp | Flintshire | Sir Y Fflint | Rhosesmor STW | 6142 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324830 | 372949 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PQ | CH65PQ | ch6 5pq | ch65pq | Flintshire | Sir Y Fflint | Rhosesmor STW | 6176 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324630 | 373144 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PR | CH65PR | ch6 5pr | ch65pr | Flintshire | Sir Y Fflint | Rhosesmor STW | 6118 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324813 | 372932 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PS | CH65PS | ch6 5ps | ch65ps | Flintshire | Sir Y Fflint | Rhosesmor STW | 6179 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324733 | 373071 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PT | CH65PT | ch6 5pt | ch65pt | Flintshire | Sir Y Fflint | Rhosesmor STW | 6146 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324991 | 372821 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PU | CH65PU | ch6 5pu | ch65pu | Flintshire | Sir Y Fflint | Connahs Quay STW | 4497 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 326328 | 371594 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PW | CH65PW | ch6 5pw | ch65pw | Flintshire | Sir Y Fflint | Rhosesmor STW | 3682 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 324068 | 370183 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PX | CH65PX | ch6 5px | ch65px | Flintshire | Sir Y Fflint | Rhosesmor STW | 5251 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324784 | 371788 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PY | CH65PY | ch6 5py | ch65py | Flintshire | Sir Y Fflint | Rhosesmor STW | 5229 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324776 | 371765 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5PZ | CH65PZ | ch6 5pz | ch65pz | Flintshire | Sir Y Fflint | Rhosesmor STW | 5258 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324861 | 371716 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QA | CH65QA | ch6 5qa | ch65qa | Flintshire | Sir Y Fflint | Rhosesmor STW | 5305 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324794 | 371855 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QB | CH65QB | ch6 5qb | ch65qb | Flintshire | Sir Y Fflint | Rhosesmor STW | 5298 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324847 | 371790 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QD | CH65QD | ch6 5qd | ch65qd | Flintshire | Sir Y Fflint | Rhosesmor STW | 5243 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324446 | 372099 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QE | CH65QE | ch6 5qe | ch65qe | Flintshire | Sir Y Fflint | Rhosesmor STW | 5341 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324731 | 371969 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QF | CH65QF | ch6 5qf | ch65qf | Flintshire | Sir Y Fflint | Rhosesmor STW | 5431 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324573 | 372238 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QG | CH65QG | ch6 5qg | ch65qg | Flintshire | Sir Y Fflint | Rhosesmor STW | 3689 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 323863 | 370475 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QH | CH65QH | ch6 5qh | ch65qh | Flintshire | Sir Y Fflint | Rhosesmor STW | 5231 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324513 | 372024 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QJ | CH65QJ | ch6 5qj | ch65qj | Flintshire | Sir Y Fflint | Rhosesmor STW | 5308 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324601 | 372047 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QL | CH65QL | ch6 5ql | ch65ql | Flintshire | Sir Y Fflint | Rhosesmor STW | 5124 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324454 | 371932 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QN | CH65QN | ch6 5qn | ch65qn | Flintshire | Sir Y Fflint | Rhosesmor STW | 3651 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 323980 | 370257 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QP | CH65QP | ch6 5qp | ch65qp | Flintshire | Sir Y Fflint | Rhosesmor STW | 3580 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 324005 | 370093 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QQ | CH65QQ | ch6 5qq | ch65qq | Flintshire | Sir Y Fflint | Rhosesmor STW | 4675 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324159 | 371594 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QR | CH65QR | ch6 5qr | ch65qr | Flintshire | Sir Y Fflint | Rhosesmor STW | 3850 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 324239 | 370229 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QS | CH65QS | ch6 5qs | ch65qs | Flintshire | Sir Y Fflint | Rhosesmor STW | 3821 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 324183 | 370261 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QT | CH65QT | ch6 5qt | ch65qt | Flintshire | Sir Y Fflint | Rhosesmor STW | 3368 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 323788 | 370038 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QU | CH65QU | ch6 5qu | ch65qu | Flintshire | Sir Y Fflint | Rhosesmor STW | 3144 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 323459 | 370108 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QW | CH65QW | ch6 5qw | ch65qw | Flintshire | Sir Y Fflint | Rhosesmor STW | 3684 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 323990 | 370300 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QX | CH65QX | ch6 5qx | ch65qx | Flintshire | Sir Y Fflint | Rhosesmor STW | 4896 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323846 | 372132 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QY | CH65QY | ch6 5qy | ch65qy | Flintshire | Sir Y Fflint | Rhosesmor STW | 3843 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 323356 | 371185 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5QZ | CH65QZ | ch6 5qz | ch65qz | Flintshire | Sir Y Fflint | Rhosesmor STW | 4923 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323816 | 372186 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RA | CH65RA | ch6 5ra | ch65ra | Flintshire | Sir Y Fflint | Rhosesmor STW | 4328 | 863 | 700to900 | 1.73 | 1.26 | 0.93 | 16.08 | 8.58 | 9.48 | 322421 | 372237 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RB | CH65RB | ch6 5rb | ch65rb | Flintshire | Sir Y Fflint | Rhosesmor STW | 4951 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323999 | 372087 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RE | CH65RE | ch6 5re | ch65re | Flintshire | Sir Y Fflint | Rhosesmor STW | 4861 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323760 | 372149 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RF | CH65RF | ch6 5rf | ch65rf | Flintshire | Sir Y Fflint | Rhosesmor STW | 4922 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323689 | 372271 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RG | CH65RG | ch6 5rg | ch65rg | Flintshire | Sir Y Fflint | Rhosesmor STW | 4781 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323629 | 372141 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RH | CH65RH | ch6 5rh | ch65rh | Flintshire | Sir Y Fflint | Rhosesmor STW | 4707 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 322824 | 372488 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RJ | CH65RJ | ch6 5rj | ch65rj | Flintshire | Sir Y Fflint | Rhosesmor STW | 4749 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 322801 | 372543 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RL | CH65RL | ch6 5rl | ch65rl | Flintshire | Sir Y Fflint | Rhosesmor STW | 4690 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 321668 | 372791 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RN | CH65RN | ch6 5rn | ch65rn | Flintshire | Sir Y Fflint | Rhosesmor STW | 4844 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323571 | 372254 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RP | CH65RP | ch6 5rp | ch65rp | Flintshire | Sir Y Fflint | Rhosesmor STW | 5280 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 322574 | 373188 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RQ | CH65RQ | ch6 5rq | ch65rq | Flintshire | Sir Y Fflint | Rhosesmor STW | 4801 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323723 | 372102 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RR | CH65RR | ch6 5rr | ch65rr | Flintshire | Sir Y Fflint | Rhosesmor STW | 6398 | 798 | 700to900 | 1.6 | 1.17 | 0.86 | 14.87 | 7.93 | 8.77 | 323435 | 374064 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RS | CH65RS | ch6 5rs | ch65rs | Flintshire | Sir Y Fflint | Rhosesmor STW | 6425 | 798 | 700to900 | 1.6 | 1.17 | 0.86 | 14.87 | 7.93 | 8.77 | 323079 | 374227 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RT | CH65RT | ch6 5rt | ch65rt | Flintshire | Sir Y Fflint | Rhosesmor STW | 6374 | 798 | 700to900 | 1.6 | 1.17 | 0.86 | 14.87 | 7.93 | 8.77 | 322976 | 374208 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RU | CH65RU | ch6 5ru | ch65ru | Flintshire | Sir Y Fflint | Rhosesmor STW | 6377 | 798 | 700to900 | 1.6 | 1.17 | 0.86 | 14.87 | 7.93 | 8.77 | 322931 | 374225 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RW | CH65RW | ch6 5rw | ch65rw | Flintshire | Sir Y Fflint | Rhosesmor STW | 4846 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323521 | 372287 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RX | CH65RX | ch6 5rx | ch65rx | Flintshire | Sir Y Fflint | Rhosesmor STW | 6396 | 798 | 700to900 | 1.6 | 1.17 | 0.86 | 14.87 | 7.93 | 8.77 | 323062 | 374202 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RY | CH65RY | ch6 5ry | ch65ry | Flintshire | Sir Y Fflint | Rhosesmor STW | 6333 | 798 | 700to900 | 1.6 | 1.17 | 0.86 | 14.87 | 7.93 | 8.77 | 323045 | 374142 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5RZ | CH65RZ | ch6 5rz | ch65rz | Flintshire | Sir Y Fflint | Rhosesmor STW | 4993 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324032 | 372115 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SA | CH65SA | ch6 5sa | ch65sa | Flintshire | Sir Y Fflint | Rhosesmor STW | 5124 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324754 | 371635 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SB | CH65SB | ch6 5sb | ch65sb | Flintshire | Sir Y Fflint | Connahs Quay STW | 5757 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325204 | 372166 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SD | CH65SD | ch6 5sd | ch65sd | Flintshire | Sir Y Fflint | Connahs Quay STW | 5290 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325647 | 372002 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SE | CH65SE | ch6 5se | ch65se | Flintshire | Sir Y Fflint | Connahs Quay STW | 5424 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325591 | 372170 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SF | CH65SF | ch6 5sf | ch65sf | Flintshire | Sir Y Fflint | Connahs Quay STW | 4925 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325970 | 371830 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SG | CH65SG | ch6 5sg | ch65sg | Flintshire | Sir Y Fflint | Rhosesmor STW | 3537 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 323948 | 370103 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SH | CH65SH | ch6 5sh | ch65sh | Flintshire | Sir Y Fflint | Rhosesmor STW | 5247 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324672 | 371896 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SL | CH65SL | ch6 5sl | ch65sl | Flintshire | Sir Y Fflint | Rhosesmor STW | 3719 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 324142 | 370138 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SN | CH65SN | ch6 5sn | ch65sn | Flintshire | Sir Y Fflint | Rhosesmor STW | 3784 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 324110 | 370304 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SP | CH65SP | ch6 5sp | ch65sp | Flintshire | Sir Y Fflint | Connahs Quay STW | 5510 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325460 | 372117 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SQ | CH65SQ | ch6 5sq | ch65sq | Flintshire | Sir Y Fflint | Rhosesmor STW | 5994 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 324587 | 372950 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SR | CH65SR | ch6 5sr | ch65sr | Flintshire | Sir Y Fflint | Connahs Quay STW | 5295 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325632 | 371984 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SS | CH65SS | ch6 5ss | ch65ss | Flintshire | Sir Y Fflint | Connahs Quay STW | 5216 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325687 | 371921 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5ST | CH65ST | ch6 5st | ch65st | Flintshire | Sir Y Fflint | Connahs Quay STW | 4784 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 325930 | 371453 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SU | CH65SU | ch6 5su | ch65su | Flintshire | Sir Y Fflint | Connahs Quay STW | 3694 | 759 | 700to900 | 1.52 | 1.11 | 0.82 | 14.15 | 7.55 | 8.34 | 326622 | 370119 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SW | CH65SW | ch6 5sw | ch65sw | Flintshire | Sir Y Fflint | Rhosesmor STW | 4848 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323540 | 372277 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SX | CH65SX | ch6 5sx | ch65sx | Flintshire | Sir Y Fflint | Connahs Quay STW | 4102 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 326448 | 370940 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SY | CH65SY | ch6 5sy | ch65sy | Flintshire | Sir Y Fflint | Connahs Quay STW | 4387 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 326294 | 371294 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SZ | CH65SZ | ch6 5sz | ch65sz | Flintshire | Sir Y Fflint | Connahs Quay STW | 4464 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 326262 | 371403 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TA | CH65TA | ch6 5ta | ch65ta | Flintshire | Sir Y Fflint | Rhosesmor STW | 5130 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324632 | 371770 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TB | CH65TB | ch6 5tb | ch65tb | Flintshire | Sir Y Fflint | Rhosesmor STW | 5070 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324601 | 371717 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TD | CH65TD | ch6 5td | ch65td | Flintshire | Sir Y Fflint | Connahs Quay STW | 4403 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 326314 | 371370 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TG | CH65TG | ch6 5tg | ch65tg | Flintshire | Sir Y Fflint | Rhosesmor STW | 5010 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324629 | 371601 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TJ | CH65TJ | ch6 5tj | ch65tj | Flintshire | Sir Y Fflint | Rhosesmor STW | 4942 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324521 | 371616 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TL | CH65TL | ch6 5tl | ch65tl | Flintshire | Sir Y Fflint | Rhosesmor STW | 5208 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324851 | 371653 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TN | CH65TN | ch6 5tn | ch65tn | Flintshire | Sir Y Fflint | Rhosesmor STW | 4948 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324597 | 371545 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TP | CH65TP | ch6 5tp | ch65tp | Flintshire | Sir Y Fflint | Rhosesmor STW | 5076 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324644 | 371682 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TQ | CH65TQ | ch6 5tq | ch65tq | Flintshire | Sir Y Fflint | Rhosesmor STW | 4960 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 324481 | 371681 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TR | CH65TR | ch6 5tr | ch65tr | Flintshire | Sir Y Fflint | Rhosesmor STW | 5002 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323592 | 372426 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TS | CH65TS | ch6 5ts | ch65ts | Flintshire | Sir Y Fflint | Rhosesmor STW | 5219 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 323402 | 372781 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TT | CH65TT | ch6 5tt | ch65tt | Flintshire | Sir Y Fflint | Rhosesmor STW | 5361 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 323450 | 372917 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TU | CH65TU | ch6 5tu | ch65tu | Flintshire | Sir Y Fflint | Rhosesmor STW | 5280 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 323400 | 372851 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TW | CH65TW | ch6 5tw | ch65tw | Flintshire | Sir Y Fflint | Rhosesmor STW | 4939 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 324631 | 371495 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TX | CH65TX | ch6 5tx | ch65tx | Flintshire | Sir Y Fflint | Rhosesmor STW | 5069 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323721 | 372425 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TY | CH65TY | ch6 5ty | ch65ty | Flintshire | Sir Y Fflint | Rhosesmor STW | 4930 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323573 | 372353 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TZ | CH65TZ | ch6 5tz | ch65tz | Flintshire | Sir Y Fflint | Rhosesmor STW | 4968 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323678 | 372332 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UA | CH65UA | ch6 5ua | ch65ua | Flintshire | Sir Y Fflint | Rhosesmor STW | 4924 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323622 | 372316 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UB | CH65UB | ch6 5ub | ch65ub | Flintshire | Sir Y Fflint | Rhosesmor STW | 5662 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324820 | 372327 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UD | CH65UD | ch6 5ud | ch65ud | Flintshire | Sir Y Fflint | Rhosesmor STW | 5606 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324819 | 372252 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UE | CH65UE | ch6 5ue | ch65ue | Flintshire | Sir Y Fflint | Rhosesmor STW | 5643 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324872 | 372253 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UF | CH65UF | ch6 5uf | ch65uf | Flintshire | Sir Y Fflint | Rhosesmor STW | 4548 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323551 | 371914 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UG | CH65UG | ch6 5ug | ch65ug | Flintshire | Sir Y Fflint | Rhosesmor STW | 4619 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323617 | 371954 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UH | CH65UH | ch6 5uh | ch65uh | Flintshire | Sir Y Fflint | Rhosesmor STW | 4669 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323740 | 371929 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UJ | CH65UJ | ch6 5uj | ch65uj | Flintshire | Sir Y Fflint | Rhosesmor STW | 4695 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323778 | 371933 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UL | CH65UL | ch6 5ul | ch65ul | Flintshire | Sir Y Fflint | Rhosesmor STW | 4096 | 801 | 700to900 | 1.6 | 1.17 | 0.86 | 14.93 | 7.96 | 8.8 | 323938 | 371002 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UN | CH65UN | ch6 5un | ch65un | Flintshire | Sir Y Fflint | Rhosesmor STW | 3862 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 324294 | 370164 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UP | CH65UP | ch6 5up | ch65up | Flintshire | Sir Y Fflint | Rhosesmor STW | 5081 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324713 | 371616 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UQ | CH65UQ | ch6 5uq | ch65uq | Flintshire | Sir Y Fflint | Rhosesmor STW | 4641 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323670 | 371944 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UR | CH65UR | ch6 5ur | ch65ur | Flintshire | Sir Y Fflint | Rhosesmor STW | 3772 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 324156 | 370213 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5US | CH65US | ch6 5us | ch65us | Flintshire | Sir Y Fflint | Rhosesmor STW | 5176 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324700 | 371767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UT | CH65UT | ch6 5ut | ch65ut | Flintshire | Sir Y Fflint | Rhosesmor STW | 5194 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324653 | 371840 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UU | CH65UU | ch6 5uu | ch65uu | Flintshire | Sir Y Fflint | Rhosesmor STW | 3956 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 324326 | 370290 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UW | CH65UW | ch6 5uw | ch65uw | Flintshire | Sir Y Fflint | Rhosesmor STW | 4753 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323763 | 372016 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UX | CH65UX | ch6 5ux | ch65ux | Flintshire | Sir Y Fflint | Rhosesmor STW | 3987 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 324280 | 370415 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UY | CH65UY | ch6 5uy | ch65uy | Flintshire | Sir Y Fflint | Rhosesmor STW | 6756 | 772 | 700to900 | 1.55 | 1.13 | 0.83 | 14.39 | 7.67 | 8.48 | 322744 | 374675 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5UZ | CH65UZ | ch6 5uz | ch65uz | Flintshire | Sir Y Fflint | Rhosesmor STW | 5625 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324217 | 372762 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WA | CH65WA | ch6 5wa | ch65wa | Flintshire | Sir Y Fflint | Rhosesmor STW | 3690 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 323958 | 370354 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WB | CH65WB | ch6 5wb | ch65wb | Flintshire | Sir Y Fflint | Connahs Quay STW | 5251 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325605 | 371845 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WD | CH65WD | ch6 5wd | ch65wd | Flintshire | Sir Y Fflint | Connahs Quay STW | 5023 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325787 | 371701 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WF | CH65WF | ch6 5wf | ch65wf | Flintshire | Sir Y Fflint | Connahs Quay STW | 5048 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325814 | 371805 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WG | CH65WG | ch6 5wg | ch65wg | Flintshire | Sir Y Fflint | Connahs Quay STW | 5028 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325754 | 371646 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WH | CH65WH | ch6 5wh | ch65wh | Flintshire | Sir Y Fflint | Connahs Quay STW | 5051 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325726 | 371642 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WJ | CH65WJ | ch6 5wj | ch65wj | Flintshire | Sir Y Fflint | Connahs Quay STW | 4997 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325764 | 371598 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WL | CH65WL | ch6 5wl | ch65wl | Flintshire | Sir Y Fflint | Connahs Quay STW | 5001 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325743 | 371563 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WN | CH65WN | ch6 5wn | ch65wn | Flintshire | Sir Y Fflint | Connahs Quay STW | 5049 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325756 | 371698 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WP | CH65WP | ch6 5wp | ch65wp | Flintshire | Sir Y Fflint | Connahs Quay STW | 5094 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325664 | 371614 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WQ | CH65WQ | ch6 5wq | ch65wq | Flintshire | Sir Y Fflint | Connahs Quay STW | 5084 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325696 | 371657 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WR | CH65WR | ch6 5wr | ch65wr | Flintshire | Sir Y Fflint | Connahs Quay STW | 5499 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 325493 | 372153 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WT | CH65WT | ch6 5wt | ch65wt | Flintshire | Sir Y Fflint | Connahs Quay STW | 5271 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325632 | 371935 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WU | CH65WU | ch6 5wu | ch65wu | Flintshire | Sir Y Fflint | Connahs Quay STW | 5231 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325618 | 371825 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WX | CH65WX | ch6 5wx | ch65wx | Flintshire | Sir Y Fflint | Connahs Quay STW | 5203 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325640 | 371808 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5WY | CH65WY | ch6 5wy | ch65wy | Flintshire | Sir Y Fflint | Connahs Quay STW | 5209 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325657 | 371853 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5XA | CH65XA | ch6 5xa | ch65xa | Flintshire | Sir Y Fflint | Rhosesmor STW | 6343 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324442 | 373476 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5XF | CH65XF | ch6 5xf | ch65xf | Flintshire | Sir Y Fflint | Connahs Quay STW | 5358 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 325538 | 371946 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5XG | CH65XG | ch6 5xg | ch65xg | Flintshire | Sir Y Fflint | Rhosesmor STW | 5213 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324886 | 371623 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5XH | CH65XH | ch6 5xh | ch65xh | Flintshire | Sir Y Fflint | Rhosesmor STW | 5291 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 324930 | 371690 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5XP | CH65XP | ch6 5xp | ch65xp | Flintshire | Sir Y Fflint | Rhosesmor STW | 4628 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323550 | 372010 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5XW | CH65XW | ch6 5xw | ch65xw | Flintshire | Sir Y Fflint | Rhosesmor STW | 4718 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323644 | 372056 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5YA | CH65YA | ch6 5ya | ch65ya | Flintshire | Sir Y Fflint | Rhosesmor STW | 5393 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 323330 | 373012 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5YB | CH65YB | ch6 5yb | ch65yb | Flintshire | Sir Y Fflint | Rhosesmor STW | 5387 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 323416 | 372963 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5YE | CH65YE | ch6 5ye | ch65ye | Flintshire | Sir Y Fflint | Rhosesmor STW | 5371 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 323381 | 372962 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5YG | CH65YG | ch6 5yg | ch65yg | Flintshire | Sir Y Fflint | Rhosesmor STW | 4767 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 323477 | 372221 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5YJ | CH65YJ | ch6 5yj | ch65yj | Flintshire | Sir Y Fflint | Rhosesmor STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323909 | 372767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5YL | CH65YL | ch6 5yl | ch65yl | Flintshire | Sir Y Fflint | Rhosesmor STW | 5605 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323939 | 372920 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5YN | CH65YN | ch6 5yn | ch65yn | Flintshire | Sir Y Fflint | Rhosesmor STW | 5716 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323937 | 373051 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5YP | CH65YP | ch6 5yp | ch65yp | Flintshire | Sir Y Fflint | Rhosesmor STW | 4845 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 323424 | 372343 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5YR | CH65YR | ch6 5yr | ch65yr | Flintshire | Sir Y Fflint | Rhosesmor STW | 4737 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 323348 | 372262 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5YS | CH65YS | ch6 5ys | ch65ys | Flintshire | Sir Y Fflint | Rhosesmor STW | 4785 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323570 | 372184 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5YT | CH65YT | ch6 5yt | ch65yt | Flintshire | Sir Y Fflint | Rhosesmor STW | 4697 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 323455 | 372153 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 5YU | CH65YU | ch6 5yu | ch65yu | Flintshire | Sir Y Fflint | Rhosesmor STW | 4813 | 785 | 700to900 | 1.57 | 1.15 | 0.84 | 14.63 | 7.8 | 8.62 | 323500 | 372261 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6AF | CH66AF | ch6 6af | ch66af | Flintshire | Sir Y Fflint | Rhosesmor STW | 7264 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322144 | 375321 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6AN | CH66AN | ch6 6an | ch66an | Flintshire | Sir Y Fflint | Rhosesmor STW | 7198 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322130 | 375256 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6AP | CH66AP | ch6 6ap | ch66ap | Flintshire | Sir Y Fflint | Rhosesmor STW | 6881 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322412 | 374882 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6AR | CH66AR | ch6 6ar | ch66ar | Flintshire | Sir Y Fflint | Rhosesmor STW | 6753 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322452 | 374743 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6AS | CH66AS | ch6 6as | ch66as | Flintshire | Sir Y Fflint | Rhosesmor STW | 6991 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322409 | 374995 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6AT | CH66AT | ch6 6at | ch66at | Flintshire | Sir Y Fflint | Rhosesmor STW | 6910 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322460 | 374902 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6AU | CH66AU | ch6 6au | ch66au | Flintshire | Sir Y Fflint | Rhosesmor STW | 6915 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322397 | 374920 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6AX | CH66AX | ch6 6ax | ch66ax | Flintshire | Sir Y Fflint | Rhosesmor STW | 7136 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322268 | 375170 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BA | CH66BA | ch6 6ba | ch66ba | Flintshire | Sir Y Fflint | Rhosesmor STW | 6354 | 798 | 700to900 | 1.6 | 1.17 | 0.86 | 14.87 | 7.93 | 8.77 | 322652 | 374283 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BB | CH66BB | ch6 6bb | ch66bb | Flintshire | Sir Y Fflint | Rhosesmor STW | 6908 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322155 | 374958 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BD | CH66BD | ch6 6bd | ch66bd | Flintshire | Sir Y Fflint | Rhosesmor STW | 6794 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322136 | 374846 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BE | CH66BE | ch6 6be | ch66be | Flintshire | Sir Y Fflint | Rhosesmor STW | 6828 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322090 | 374888 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BG | CH66BG | ch6 6bg | ch66bg | Flintshire | Sir Y Fflint | Rhosesmor STW | 6986 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322040 | 375056 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BH | CH66BH | ch6 6bh | ch66bh | Flintshire | Sir Y Fflint | Rhosesmor STW | 7139 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322101 | 375201 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BJ | CH66BJ | ch6 6bj | ch66bj | Flintshire | Sir Y Fflint | Rhosesmor STW | 6918 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322042 | 374987 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BL | CH66BL | ch6 6bl | ch66bl | Flintshire | Sir Y Fflint | Rhosesmor STW | 6924 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321972 | 375003 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BN | CH66BN | ch6 6bn | ch66bn | Flintshire | Sir Y Fflint | Rhosesmor STW | 7100 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322034 | 375172 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BP | CH66BP | ch6 6bp | ch66bp | Flintshire | Sir Y Fflint | Rhosesmor STW | 6875 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321902 | 374963 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BQ | CH66BQ | ch6 6bq | ch66bq | Flintshire | Sir Y Fflint | Rhosesmor STW | 7111 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322111 | 375171 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BR | CH66BR | ch6 6br | ch66br | Flintshire | Sir Y Fflint | Rhosesmor STW | 6878 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322075 | 374941 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BS | CH66BS | ch6 6bs | ch66bs | Flintshire | Sir Y Fflint | Rhosesmor STW | 6706 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322067 | 374768 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BT | CH66BT | ch6 6bt | ch66bt | Flintshire | Sir Y Fflint | Rhosesmor STW | 6729 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322097 | 374787 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BU | CH66BU | ch6 6bu | ch66bu | Flintshire | Sir Y Fflint | Rhosesmor STW | 6724 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321966 | 374802 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BW | CH66BW | ch6 6bw | ch66bw | Flintshire | Sir Y Fflint | Rhosesmor STW | 7149 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322055 | 375218 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BX | CH66BX | ch6 6bx | ch66bx | Flintshire | Sir Y Fflint | Rhosesmor STW | 6573 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322088 | 374630 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BY | CH66BY | ch6 6by | ch66by | Flintshire | Sir Y Fflint | Rhosesmor STW | 6694 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322277 | 374719 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6BZ | CH66BZ | ch6 6bz | ch66bz | Flintshire | Sir Y Fflint | Rhosesmor STW | 6417 | 834 | 700to900 | 1.67 | 1.22 | 0.9 | 15.54 | 8.29 | 9.16 | 322413 | 374407 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DA | CH66DA | ch6 6da | ch66da | Flintshire | Sir Y Fflint | Rhosesmor STW | 6329 | 834 | 700to900 | 1.67 | 1.22 | 0.9 | 15.54 | 8.29 | 9.16 | 322261 | 374350 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DB | CH66DB | ch6 6db | ch66db | Flintshire | Sir Y Fflint | Rhosesmor STW | 6550 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322324 | 374563 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DD | CH66DD | ch6 6dd | ch66dd | Flintshire | Sir Y Fflint | Rhosesmor STW | 6718 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322410 | 374716 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DE | CH66DE | ch6 6de | ch66de | Flintshire | Sir Y Fflint | Rhosesmor STW | 6599 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322393 | 374598 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DF | CH66DF | ch6 6df | ch66df | Flintshire | Sir Y Fflint | Rhosesmor STW | 6482 | 834 | 700to900 | 1.67 | 1.22 | 0.9 | 15.54 | 8.29 | 9.16 | 322355 | 374487 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DG | CH66DG | ch6 6dg | ch66dg | Flintshire | Sir Y Fflint | Rhosesmor STW | 6466 | 798 | 700to900 | 1.6 | 1.17 | 0.86 | 14.87 | 7.93 | 8.77 | 322575 | 374419 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DH | CH66DH | ch6 6dh | ch66dh | Flintshire | Sir Y Fflint | Rhosesmor STW | 6184 | 798 | 700to900 | 1.6 | 1.17 | 0.86 | 14.87 | 7.93 | 8.77 | 322695 | 374095 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DJ | CH66DJ | ch6 6dj | ch66dj | Flintshire | Sir Y Fflint | Rhosesmor STW | 6415 | 834 | 700to900 | 1.67 | 1.22 | 0.9 | 15.54 | 8.29 | 9.16 | 322496 | 374386 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DL | CH66DL | ch6 6dl | ch66dl | Flintshire | Sir Y Fflint | Rhosesmor STW | 6425 | 798 | 700to900 | 1.6 | 1.17 | 0.86 | 14.87 | 7.93 | 8.77 | 322571 | 374378 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DN | CH66DN | ch6 6dn | ch66dn | Flintshire | Sir Y Fflint | Rhosesmor STW | 6335 | 834 | 700to900 | 1.67 | 1.22 | 0.9 | 15.54 | 8.29 | 9.16 | 322484 | 374307 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DP | CH66DP | ch6 6dp | ch66dp | Flintshire | Sir Y Fflint | Rhosesmor STW | 6264 | 834 | 700to900 | 1.67 | 1.22 | 0.9 | 15.54 | 8.29 | 9.16 | 322437 | 374245 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DR | CH66DR | ch6 6dr | ch66dr | Flintshire | Sir Y Fflint | Rhosesmor STW | 6031 | 834 | 700to900 | 1.67 | 1.22 | 0.9 | 15.54 | 8.29 | 9.16 | 322099 | 374078 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DS | CH66DS | ch6 6ds | ch66ds | Flintshire | Sir Y Fflint | Rhosesmor STW | 6135 | 834 | 700to900 | 1.67 | 1.22 | 0.9 | 15.54 | 8.29 | 9.16 | 322228 | 374159 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DT | CH66DT | ch6 6dt | ch66dt | Flintshire | Sir Y Fflint | Rhosesmor STW | 5496 | 856 | 700to900 | 1.71 | 1.25 | 0.92 | 15.95 | 8.51 | 9.4 | 320858 | 373642 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DW | CH66DW | ch6 6dw | ch66dw | Flintshire | Sir Y Fflint | Rhosesmor STW | 6332 | 798 | 700to900 | 1.6 | 1.17 | 0.86 | 14.87 | 7.93 | 8.77 | 322556 | 374286 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DY | CH66DY | ch6 6dy | ch66dy | Flintshire | Sir Y Fflint | Rhosesmor STW | 6656 | 772 | 700to900 | 1.55 | 1.13 | 0.83 | 14.39 | 7.67 | 8.48 | 322616 | 374605 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6DZ | CH66DZ | ch6 6dz | ch66dz | Flintshire | Sir Y Fflint | Rhosesmor STW | 6640 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322492 | 374618 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EA | CH66EA | ch6 6ea | ch66ea | Flintshire | Sir Y Fflint | Rhosesmor STW | 6524 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322485 | 374501 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EB | CH66EB | ch6 6eb | ch66eb | Flintshire | Sir Y Fflint | Rhosesmor STW | 6568 | 772 | 700to900 | 1.55 | 1.13 | 0.83 | 14.39 | 7.67 | 8.48 | 322565 | 374527 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6ED | CH66ED | ch6 6ed | ch66ed | Flintshire | Sir Y Fflint | Rhosesmor STW | 7244 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321921 | 375333 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EE | CH66EE | ch6 6ee | ch66ee | Flintshire | Sir Y Fflint | Rhosesmor STW | 6608 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322313 | 374624 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EF | CH66EF | ch6 6ef | ch66ef | Flintshire | Sir Y Fflint | Rhosesmor STW | 7352 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321847 | 375451 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EG | CH66EG | ch6 6eg | ch66eg | Flintshire | Sir Y Fflint | Rhosesmor STW | 7323 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321832 | 375423 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EH | CH66EH | ch6 6eh | ch66eh | Flintshire | Sir Y Fflint | Rhosesmor STW | 6894 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321806 | 374994 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EL | CH66EL | ch6 6el | ch66el | Flintshire | Sir Y Fflint | Rhosesmor STW | 7075 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321842 | 375172 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EP | CH66EP | ch6 6ep | ch66ep | Flintshire | Sir Y Fflint | Rhosesmor STW | 7041 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321759 | 375148 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EQ | CH66EQ | ch6 6eq | ch66eq | Flintshire | Sir Y Fflint | Rhosesmor STW | 7167 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321919 | 375255 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6ER | CH66ER | ch6 6er | ch66er | Flintshire | Sir Y Fflint | Rhosesmor STW | 7345 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 319998 | 375424 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6ES | CH66ES | ch6 6es | ch66es | Flintshire | Sir Y Fflint | Rhosesmor STW | 6235 | 856 | 700to900 | 1.71 | 1.25 | 0.92 | 15.95 | 8.51 | 9.4 | 321355 | 374373 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6ET | CH66ET | ch6 6et | ch66et | Flintshire | Sir Y Fflint | Rhosesmor STW | 5904 | 856 | 700to900 | 1.71 | 1.25 | 0.92 | 15.95 | 8.51 | 9.4 | 320613 | 374039 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EU | CH66EU | ch6 6eu | ch66eu | Flintshire | Sir Y Fflint | Rhosesmor STW | 6987 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321775 | 375092 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EW | CH66EW | ch6 6ew | ch66ew | Flintshire | Sir Y Fflint | Rhosesmor STW | 6981 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321972 | 375061 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EX | CH66EX | ch6 6ex | ch66ex | Flintshire | Sir Y Fflint | Rhosesmor STW | 6997 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322005 | 375072 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EY | CH66EY | ch6 6ey | ch66ey | Flintshire | Sir Y Fflint | Rhosesmor STW | 7038 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321586 | 375161 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6EZ | CH66EZ | ch6 6ez | ch66ez | Flintshire | Sir Y Fflint | Rhosesmor STW | 7002 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321639 | 375121 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6FB | CH66FB | ch6 6fb | ch66fb | Flintshire | Sir Y Fflint | Rhosesmor STW | 7021 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321944 | 375105 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HA | CH66HA | ch6 6ha | ch66ha | Flintshire | Sir Y Fflint | Rhosesmor STW | 7007 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321535 | 375134 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HB | CH66HB | ch6 6hb | ch66hb | Flintshire | Sir Y Fflint | Rhosesmor STW | 6941 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 321529 | 375069 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HD | CH66HD | ch6 6hd | ch66hd | Flintshire | Sir Y Fflint | Rhosesmor STW | 8118 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320917 | 376265 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HE | CH66HE | ch6 6he | ch66he | Flintshire | Sir Y Fflint | Rhosesmor STW | 7595 | 777 | 700to900 | 1.56 | 1.14 | 0.83 | 14.48 | 7.72 | 8.54 | 321583 | 375720 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HF | CH66HF | ch6 6hf | ch66hf | Flintshire | Sir Y Fflint | Rhosesmor STW | 7638 | 777 | 700to900 | 1.56 | 1.14 | 0.83 | 14.48 | 7.72 | 8.54 | 321531 | 375767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HG | CH66HG | ch6 6hg | ch66hg | Flintshire | Sir Y Fflint | Rhosesmor STW | 7995 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 321046 | 376142 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HH | CH66HH | ch6 6hh | ch66hh | Flintshire | Sir Y Fflint | Rhosesmor STW | 7472 | 777 | 700to900 | 1.56 | 1.14 | 0.83 | 14.48 | 7.72 | 8.54 | 321739 | 375583 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HJ | CH66HJ | ch6 6hj | ch66hj | Flintshire | Sir Y Fflint | Rhosesmor STW | 8003 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 321251 | 376146 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HL | CH66HL | ch6 6hl | ch66hl | Flintshire | Sir Y Fflint | Rhosesmor STW | 7559 | 777 | 700to900 | 1.56 | 1.14 | 0.83 | 14.48 | 7.72 | 8.54 | 321622 | 375681 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HN | CH66HN | ch6 6hn | ch66hn | Flintshire | Sir Y Fflint | Rhosesmor STW | 7424 | 777 | 700to900 | 1.56 | 1.14 | 0.83 | 14.48 | 7.72 | 8.54 | 321807 | 375528 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HP | CH66HP | ch6 6hp | ch66hp | Flintshire | Sir Y Fflint | Rhosesmor STW | 7553 | 777 | 700to900 | 1.56 | 1.14 | 0.83 | 14.48 | 7.72 | 8.54 | 321646 | 375673 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HQ | CH66HQ | ch6 6hq | ch66hq | Flintshire | Sir Y Fflint | Rhosesmor STW | 7450 | 777 | 700to900 | 1.56 | 1.14 | 0.83 | 14.48 | 7.72 | 8.54 | 321757 | 375559 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HR | CH66HR | ch6 6hr | ch66hr | Flintshire | Sir Y Fflint | Rhosesmor STW | 7525 | 777 | 700to900 | 1.56 | 1.14 | 0.83 | 14.48 | 7.72 | 8.54 | 321699 | 375640 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HT | CH66HT | ch6 6ht | ch66ht | Flintshire | Sir Y Fflint | Rhosesmor STW | 8159 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 321043 | 376306 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HU | CH66HU | ch6 6hu | ch66hu | Flintshire | Sir Y Fflint | Rhosesmor STW | 7388 | 777 | 700to900 | 1.56 | 1.14 | 0.83 | 14.48 | 7.72 | 8.54 | 321662 | 375506 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HW | CH66HW | ch6 6hw | ch66hw | Flintshire | Sir Y Fflint | Rhosesmor STW | 8286 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320817 | 376431 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6HZ | CH66HZ | ch6 6hz | ch66hz | Flintshire | Sir Y Fflint | Rhosesmor STW | 7673 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 321209 | 375818 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JA | CH66JA | ch6 6ja | ch66ja | Flintshire | Sir Y Fflint | Rhosesmor STW | 8138 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320518 | 376271 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JB | CH66JB | ch6 6jb | ch66jb | Flintshire | Sir Y Fflint | Rhosesmor STW | 8433 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 320709 | 376575 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JD | CH66JD | ch6 6jd | ch66jd | Flintshire | Sir Y Fflint | Rhosesmor STW | 8532 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 320617 | 376671 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JE | CH66JE | ch6 6je | ch66je | Flintshire | Sir Y Fflint | Rhosesmor STW | 8295 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320911 | 376442 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JF | CH66JF | ch6 6jf | ch66jf | Flintshire | Sir Y Fflint | Rhosesmor STW | 8376 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 320759 | 376520 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JG | CH66JG | ch6 6jg | ch66jg | Flintshire | Sir Y Fflint | Rhosesmor STW | 8389 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 320743 | 376532 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JH | CH66JH | ch6 6jh | ch66jh | Flintshire | Sir Y Fflint | Rhosesmor STW | 8181 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320878 | 376327 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JJ | CH66JJ | ch6 6jj | ch66jj | Flintshire | Sir Y Fflint | Rhosesmor STW | 8581 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320464 | 376711 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JL | CH66JL | ch6 6jl | ch66jl | Flintshire | Sir Y Fflint | Rhosesmor STW | 8467 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320448 | 376596 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JN | CH66JN | ch6 6jn | ch66jn | Flintshire | Sir Y Fflint | Rhosesmor STW | 8336 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320574 | 376472 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JP | CH66JP | ch6 6jp | ch66jp | Flintshire | Sir Y Fflint | Rhosesmor STW | 8258 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 320405 | 376384 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JQ | CH66JQ | ch6 6jq | ch66jq | Flintshire | Sir Y Fflint | Rhosesmor STW | 8369 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 320677 | 376510 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JR | CH66JR | ch6 6jr | ch66jr | Flintshire | Sir Y Fflint | Rhosesmor STW | 8388 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 320500 | 376520 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JS | CH66JS | ch6 6js | ch66js | Flintshire | Sir Y Fflint | Rhosesmor STW | 8117 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 320230 | 376228 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JT | CH66JT | ch6 6jt | ch66jt | Flintshire | Sir Y Fflint | Rhosesmor STW | 8230 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320525 | 376364 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JU | CH66JU | ch6 6ju | ch66ju | Flintshire | Sir Y Fflint | Rhosesmor STW | 8319 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320639 | 376458 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JW | CH66JW | ch6 6jw | ch66jw | Flintshire | Sir Y Fflint | Rhosesmor STW | 8354 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 320416 | 376481 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JX | CH66JX | ch6 6jx | ch66jx | Flintshire | Sir Y Fflint | Rhosesmor STW | 8168 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320908 | 376315 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JY | CH66JY | ch6 6jy | ch66jy | Flintshire | Sir Y Fflint | Rhosesmor STW | 8242 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320853 | 376388 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6JZ | CH66JZ | ch6 6jz | ch66jz | Flintshire | Sir Y Fflint | Rhosesmor STW | 8222 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320639 | 376361 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LA | CH66LA | ch6 6la | ch66la | Flintshire | Sir Y Fflint | Rhosesmor STW | 8532 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320416 | 376659 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LD | CH66LD | ch6 6ld | ch66ld | Flintshire | Sir Y Fflint | Rhosesmor STW | 7649 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320666 | 375789 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LF | CH66LF | ch6 6lf | ch66lf | Flintshire | Sir Y Fflint | Rhosesmor STW | 8115 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320817 | 376260 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LG | CH66LG | ch6 6lg | ch66lg | Flintshire | Sir Y Fflint | Rhosesmor STW | 8108 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320795 | 376253 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LH | CH66LH | ch6 6lh | ch66lh | Flintshire | Sir Y Fflint | Rhosesmor STW | 8065 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320795 | 376210 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LJ | CH66LJ | ch6 6lj | ch66lj | Flintshire | Sir Y Fflint | Rhosesmor STW | 8097 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320837 | 376243 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LL | CH66LL | ch6 6ll | ch66ll | Flintshire | Sir Y Fflint | Rhosesmor STW | 8150 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320878 | 376296 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LN | CH66LN | ch6 6ln | ch66ln | Flintshire | Sir Y Fflint | Rhosesmor STW | 8147 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320862 | 376293 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LP | CH66LP | ch6 6lp | ch66lp | Flintshire | Sir Y Fflint | Rhosesmor STW | 8145 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320803 | 376290 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LQ | CH66LQ | ch6 6lq | ch66lq | Flintshire | Sir Y Fflint | Rhosesmor STW | 8099 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320773 | 376243 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LR | CH66LR | ch6 6lr | ch66lr | Flintshire | Sir Y Fflint | Rhosesmor STW | 8126 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320787 | 376271 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LS | CH66LS | ch6 6ls | ch66ls | Flintshire | Sir Y Fflint | Rhosesmor STW | 6397 | 834 | 700to900 | 1.67 | 1.22 | 0.9 | 15.54 | 8.29 | 9.16 | 322272 | 374417 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LT | CH66LT | ch6 6lt | ch66lt | Flintshire | Sir Y Fflint | Rhosesmor STW | 6500 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 322298 | 374517 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LU | CH66LU | ch6 6lu | ch66lu | Flintshire | Sir Y Fflint | Rhosesmor STW | 8046 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320811 | 376191 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LW | CH66LW | ch6 6lw | ch66lw | Flintshire | Sir Y Fflint | Rhosesmor STW | 8140 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320841 | 376286 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 6LY | CH66LY | ch6 6ly | ch66ly | Flintshire | Sir Y Fflint | Rhosesmor STW | 8007 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 320809 | 376152 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 9BL | CH69BL | ch6 9bl | ch69bl | Flintshire | Sir Y Fflint | Rhosesmor STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323909 | 372767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 9DW | CH69DW | ch6 9dw | ch69dw | Flintshire | Sir Y Fflint | Rhosesmor STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323909 | 372767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 9EA | CH69EA | ch6 9ea | ch69ea | Flintshire | Sir Y Fflint | Rhosesmor STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323909 | 372767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 9EG | CH69EG | ch6 9eg | ch69eg | Flintshire | Sir Y Fflint | Rhosesmor STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323909 | 372767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 9EN | CH69EN | ch6 9en | ch69en | Flintshire | Sir Y Fflint | Rhosesmor STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323909 | 372767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 9EQ | CH69EQ | ch6 9eq | ch69eq | Flintshire | Sir Y Fflint | Rhosesmor STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323909 | 372767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 9EU | CH69EU | ch6 9eu | ch69eu | Flintshire | Sir Y Fflint | Rhosesmor STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323909 | 372767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH6 9EX | CH69EX | ch6 9ex | ch69ex | Flintshire | Sir Y Fflint | Rhosesmor STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323909 | 372767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AA | CH76AA | ch7 6aa | ch76aa | Flintshire | Sir Y Fflint | Rhosesmor STW | 2758 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 323642 | 368938 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AF | CH76AF | ch7 6af | ch76af | Flintshire | Sir Y Fflint | Rhosesmor STW | 2737 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 323676 | 367579 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AG | CH76AG | ch7 6ag | ch76ag | Flintshire | Sir Y Fflint | Rhosesmor STW | 1666 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 322424 | 369014 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AL | CH76AL | ch7 6al | ch76al | Flintshire | Sir Y Fflint | Rhosesmor STW | 1224 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 321950 | 368921 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AN | CH76AN | ch7 6an | ch76an | Flintshire | Sir Y Fflint | Rhosesmor STW | 2918 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 323881 | 368607 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AQ | CH76AQ | ch7 6aq | ch76aq | Flintshire | Sir Y Fflint | Rhosesmor STW | 2100 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 322707 | 369372 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AR | CH76AR | ch7 6ar | ch76ar | Flintshire | Sir Y Fflint | Rhosesmor STW | 2839 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 323766 | 368786 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AT | CH76AT | ch7 6at | ch76at | Flintshire | Sir Y Fflint | Rhosesmor STW | 3275 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324261 | 368436 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AU | CH76AU | ch7 6au | ch76au | Flintshire | Sir Y Fflint | Rhosesmor STW | 3331 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 324307 | 368541 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AW | CH76AW | ch7 6aw | ch76aw | Flintshire | Sir Y Fflint | Rhosesmor STW | 3303 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324300 | 368263 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AX | CH76AX | ch7 6ax | ch76ax | Flintshire | Sir Y Fflint | Rhosesmor STW | 3384 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324369 | 368458 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AY | CH76AY | ch7 6ay | ch76ay | Flintshire | Sir Y Fflint | Rhosesmor STW | 3359 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 324339 | 368510 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BA | CH76BA | ch7 6ba | ch76ba | Flintshire | Sir Y Fflint | Rhosesmor STW | 2857 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 323816 | 368625 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BB | CH76BB | ch7 6bb | ch76bb | Flintshire | Sir Y Fflint | Rhosesmor STW | 3039 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324038 | 368193 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BD | CH76BD | ch7 6bd | ch76bd | Flintshire | Sir Y Fflint | Rhosesmor STW | 3101 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324098 | 368250 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BE | CH76BE | ch7 6be | ch76be | Flintshire | Sir Y Fflint | Rhosesmor STW | 3357 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324325 | 367692 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BF | CH76BF | ch7 6bf | ch76bf | Flintshire | Sir Y Fflint | Rhosesmor STW | 3429 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324416 | 368440 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BH | CH76BH | ch7 6bh | ch76bh | Flintshire | Sir Y Fflint | Rhosesmor STW | 3468 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324458 | 368393 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BL | CH76BL | ch7 6bl | ch76bl | Flintshire | Sir Y Fflint | Rhosesmor STW | 3359 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324352 | 368343 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BN | CH76BN | ch7 6bn | ch76bn | Flintshire | Sir Y Fflint | Rhosesmor STW | 3413 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324406 | 368345 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BP | CH76BP | ch7 6bp | ch76bp | Flintshire | Sir Y Fflint | Rhosesmor STW | 3631 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 324619 | 368436 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BQ | CH76BQ | ch7 6bq | ch76bq | Flintshire | Sir Y Fflint | Rhosesmor STW | 3456 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324446 | 368391 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BR | CH76BR | ch7 6br | ch76br | Flintshire | Sir Y Fflint | Rhosesmor STW | 3586 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 324522 | 368816 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BS | CH76BS | ch7 6bs | ch76bs | Flintshire | Sir Y Fflint | Rhosesmor STW | 3829 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 324816 | 368452 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BT | CH76BT | ch7 6bt | ch76bt | Flintshire | Sir Y Fflint | Rhosesmor STW | 4492 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 325482 | 368427 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BU | CH76BU | ch7 6bu | ch76bu | Flintshire | Sir Y Fflint | Rhosesmor STW | 3744 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 324728 | 368485 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BW | CH76BW | ch7 6bw | ch76bw | Flintshire | Sir Y Fflint | Rhosesmor STW | 3390 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324383 | 368355 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DB | CH76DB | ch7 6db | ch76db | Flintshire | Sir Y Fflint | Rhosesmor STW | 3964 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 324954 | 368409 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DD | CH76DD | ch7 6dd | ch76dd | Flintshire | Sir Y Fflint | Rhosesmor STW | 4088 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 325077 | 368435 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DG | CH76DG | ch7 6dg | ch76dg | Flintshire | Sir Y Fflint | Rhosesmor STW | 4584 | 792 | 700to900 | 1.59 | 1.16 | 0.85 | 14.76 | 7.87 | 8.7 | 325354 | 369579 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DJ | CH76DJ | ch7 6dj | ch76dj | Flintshire | Sir Y Fflint | Rhosesmor STW | 3299 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324295 | 368280 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DL | CH76DL | ch7 6dl | ch76dl | Flintshire | Sir Y Fflint | Rhosesmor STW | 4436 | 792 | 700to900 | 1.59 | 1.16 | 0.85 | 14.76 | 7.87 | 8.7 | 324829 | 370387 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DN | CH76DN | ch7 6dn | ch76dn | Flintshire | Sir Y Fflint | Rhosesmor STW | 4242 | 792 | 700to900 | 1.59 | 1.16 | 0.85 | 14.76 | 7.87 | 8.7 | 324646 | 370316 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DP | CH76DP | ch7 6dp | ch76dp | Flintshire | Sir Y Fflint | Rhosesmor STW | 3504 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 324475 | 368590 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DR | CH76DR | ch7 6dr | ch76dr | Flintshire | Sir Y Fflint | Rhosesmor STW | 3532 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 324498 | 368632 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DS | CH76DS | ch7 6ds | ch76ds | Flintshire | Sir Y Fflint | Rhosesmor STW | 3489 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 324446 | 368688 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DT | CH76DT | ch7 6dt | ch76dt | Flintshire | Sir Y Fflint | Rhosesmor STW | 3581 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 324537 | 368703 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EH | CH76EH | ch7 6eh | ch76eh | Flintshire | Sir Y Fflint | Rhosesmor STW | 3130 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324121 | 368377 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EU | CH76EU | ch7 6eu | ch76eu | Flintshire | Sir Y Fflint | Rhosesmor STW | 3559 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 324540 | 368501 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GP | CH76GP | ch7 6gp | ch76gp | Flintshire | Sir Y Fflint | Rhosesmor STW | 3843 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 324837 | 368349 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GQ | CH76GQ | ch7 6gq | ch76gq | Flintshire | Sir Y Fflint | Rhosesmor STW | 3987 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 324980 | 368358 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GR | CH76GR | ch7 6gr | ch76gr | Flintshire | Sir Y Fflint | Rhosesmor STW | 4106 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 325100 | 368336 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LS | CH76LS | ch7 6ls | ch76ls | Flintshire | Sir Y Fflint | Mold WwTW | 3059 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 323989 | 366102 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LT | CH76LT | ch7 6lt | ch76lt | Flintshire | Sir Y Fflint | Rhydymwyn STW | 3034 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 323905 | 366090 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PJ | CH76PJ | ch7 6pj | ch76pj | Flintshire | Sir Y Fflint | Rhosesmor STW | 1081 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 321438 | 369138 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PP | CH76PP | ch7 6pp | ch76pp | Flintshire | Sir Y Fflint | Rhosesmor STW | 714 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 321205 | 368834 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PR | CH76PR | ch7 6pr | ch76pr | Flintshire | Sir Y Fflint | Rhosesmor STW | 1483 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 321048 | 369632 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PS | CH76PS | ch7 6ps | ch76ps | Flintshire | Sir Y Fflint | Rhosesmor STW | 1248 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320929 | 369396 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PT | CH76PT | ch7 6pt | ch76pt | Flintshire | Sir Y Fflint | Rhosesmor STW | 673 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 321292 | 368756 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PU | CH76PU | ch7 6pu | ch76pu | Flintshire | Sir Y Fflint | Rhosesmor STW | 1490 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 320738 | 369616 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QF | CH76QF | ch7 6qf | ch76qf | Flintshire | Sir Y Fflint | Rhosesmor STW | 3492 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 324470 | 368533 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WF | CH76WF | ch7 6wf | ch76wf | Flintshire | Sir Y Fflint | Rhosesmor STW | 796 | 913 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.02 | 9.08 | 10.03 | 321503 | 368767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WJ | CH76WJ | ch7 6wj | ch76wj | Flintshire | Sir Y Fflint | Rhosesmor STW | 703 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 321485 | 368659 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WW | CH76WW | ch7 6ww | ch76ww | Flintshire | Sir Y Fflint | Rhosesmor STW | 3322 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 324316 | 368338 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YU | CH76YU | ch7 6yu | ch76yu | Flintshire | Sir Y Fflint | Rhosesmor STW | 3344 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 324307 | 368638 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AA | CH87AA | ch8 7aa | ch87aa | Flintshire | Sir Y Fflint | Rhosesmor STW | 7990 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318665 | 375789 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AD | CH87AD | ch8 7ad | ch87ad | Flintshire | Sir Y Fflint | Rhosesmor STW | 8031 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319026 | 375932 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AE | CH87AE | ch8 7ae | ch87ae | Flintshire | Sir Y Fflint | Rhosesmor STW | 8100 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318898 | 375970 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AF | CH87AF | ch8 7af | ch87af | Flintshire | Sir Y Fflint | Rhosesmor STW | 8111 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318947 | 375994 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AG | CH87AG | ch8 7ag | ch87ag | Flintshire | Sir Y Fflint | Rhosesmor STW | 8214 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318966 | 376105 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AH | CH87AH | ch8 7ah | ch87ah | Flintshire | Sir Y Fflint | Rhosesmor STW | 8379 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318853 | 376246 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AJ | CH87AJ | ch8 7aj | ch87aj | Flintshire | Sir Y Fflint | Rhosesmor STW | 8499 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318732 | 376338 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AL | CH87AL | ch8 7al | ch87al | Flintshire | Sir Y Fflint | Rhosesmor STW | 8448 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318862 | 376320 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AN | CH87AN | ch8 7an | ch87an | Flintshire | Sir Y Fflint | Rhosesmor STW | 8174 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318865 | 376038 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AP | CH87AP | ch8 7ap | ch87ap | Flintshire | Sir Y Fflint | Rhosesmor STW | 8458 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318771 | 376306 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AQ | CH87AQ | ch8 7aq | ch87aq | Flintshire | Sir Y Fflint | Rhosesmor STW | 8264 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319421 | 376259 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AR | CH87AR | ch8 7ar | ch87ar | Flintshire | Sir Y Fflint | Rhosesmor STW | 8430 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318806 | 376287 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AS | CH87AS | ch8 7as | ch87as | Flintshire | Sir Y Fflint | Rhosesmor STW | 8476 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318862 | 376349 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AT | CH87AT | ch8 7at | ch87at | Flintshire | Sir Y Fflint | Rhosesmor STW | 8549 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318881 | 376429 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AU | CH87AU | ch8 7au | ch87au | Flintshire | Sir Y Fflint | Rhosesmor STW | 8591 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318969 | 376495 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AW | CH87AW | ch8 7aw | ch87aw | Flintshire | Sir Y Fflint | Rhosesmor STW | 8403 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318912 | 376287 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AX | CH87AX | ch8 7ax | ch87ax | Flintshire | Sir Y Fflint | Rhosesmor STW | 8545 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318910 | 376433 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AY | CH87AY | ch8 7ay | ch87ay | Flintshire | Sir Y Fflint | Rhosesmor STW | 8223 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319261 | 376184 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7AZ | CH87AZ | ch8 7az | ch87az | Flintshire | Sir Y Fflint | Rhosesmor STW | 8281 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319340 | 376260 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BA | CH87BA | ch8 7ba | ch87ba | Flintshire | Sir Y Fflint | Rhosesmor STW | 8216 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319322 | 376190 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BB | CH87BB | ch8 7bb | ch87bb | Flintshire | Sir Y Fflint | Rhosesmor STW | 7922 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319050 | 375826 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BD | CH87BD | ch8 7bd | ch87bd | Flintshire | Sir Y Fflint | Rhosesmor STW | 8064 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319383 | 376048 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BE | CH87BE | ch8 7be | ch87be | Flintshire | Sir Y Fflint | Rhosesmor STW | 8026 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319350 | 376002 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BG | CH87BG | ch8 7bg | ch87bg | Flintshire | Sir Y Fflint | Rhosesmor STW | 8033 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319438 | 376027 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BH | CH87BH | ch8 7bh | ch87bh | Flintshire | Sir Y Fflint | Rhosesmor STW | 7942 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319261 | 375897 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BJ | CH87BJ | ch8 7bj | ch87bj | Flintshire | Sir Y Fflint | Rhosesmor STW | 8120 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319356 | 376099 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BL | CH87BL | ch8 7bl | ch87bl | Flintshire | Sir Y Fflint | Rhosesmor STW | 7920 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319138 | 375845 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BN | CH87BN | ch8 7bn | ch87bn | Flintshire | Sir Y Fflint | Rhosesmor STW | 7891 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319297 | 375852 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BP | CH87BP | ch8 7bp | ch87bp | Flintshire | Sir Y Fflint | Rhosesmor STW | 8182 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319198 | 376128 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BQ | CH87BQ | ch8 7bq | ch87bq | Flintshire | Sir Y Fflint | Rhosesmor STW | 8286 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319273 | 376251 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BR | CH87BR | ch8 7br | ch87br | Flintshire | Sir Y Fflint | Rhosesmor STW | 8118 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319429 | 376112 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BS | CH87BS | ch8 7bs | ch87bs | Flintshire | Sir Y Fflint | Rhosesmor STW | 7999 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319401 | 375985 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BT | CH87BT | ch8 7bt | ch87bt | Flintshire | Sir Y Fflint | Rhosesmor STW | 7947 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319405 | 375933 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BU | CH87BU | ch8 7bu | ch87bu | Flintshire | Sir Y Fflint | Rhosesmor STW | 7991 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319475 | 375992 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BW | CH87BW | ch8 7bw | ch87bw | Flintshire | Sir Y Fflint | Rhosesmor STW | 7891 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319217 | 375834 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BX | CH87BX | ch8 7bx | ch87bx | Flintshire | Sir Y Fflint | Rhosesmor STW | 8149 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319439 | 376145 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BY | CH87BY | ch8 7by | ch87by | Flintshire | Sir Y Fflint | Rhosesmor STW | 8184 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319303 | 376153 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7BZ | CH87BZ | ch8 7bz | ch87bz | Flintshire | Sir Y Fflint | Rhosesmor STW | 8142 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319309 | 376112 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DA | CH87DA | ch8 7da | ch87da | Flintshire | Sir Y Fflint | Rhosesmor STW | 9386 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 317536 | 376870 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DB | CH87DB | ch8 7db | ch87db | Flintshire | Sir Y Fflint | Rhosesmor STW | 9291 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 317509 | 376757 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DD | CH87DD | ch8 7dd | ch87dd | Flintshire | Sir Y Fflint | Rhosesmor STW | 9261 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 317174 | 376581 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DE | CH87DE | ch8 7de | ch87de | Flintshire | Sir Y Fflint | Rhosesmor STW | 9444 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316817 | 376614 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DF | CH87DF | ch8 7df | ch87df | Flintshire | Sir Y Fflint | Rhosesmor STW | 9308 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316977 | 376540 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DG | CH87DG | ch8 7dg | ch87dg | Flintshire | Sir Y Fflint | Rhosesmor STW | 9455 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316865 | 376650 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DH | CH87DH | ch8 7dh | ch87dh | Flintshire | Sir Y Fflint | Rhosesmor STW | 9423 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316979 | 376669 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DJ | CH87DJ | ch8 7dj | ch87dj | Flintshire | Sir Y Fflint | Rhosesmor STW | 9395 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316943 | 376621 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DL | CH87DL | ch8 7dl | ch87dl | Flintshire | Sir Y Fflint | Rhosesmor STW | 9329 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 317055 | 376601 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DN | CH87DN | ch8 7dn | ch87dn | Flintshire | Sir Y Fflint | Rhosesmor STW | 9210 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 317526 | 376677 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DP | CH87DP | ch8 7dp | ch87dp | Flintshire | Sir Y Fflint | Rhosesmor STW | 8273 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 319645 | 376309 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DQ | CH87DQ | ch8 7dq | ch87dq | Flintshire | Sir Y Fflint | Rhosesmor STW | 9507 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316885 | 376717 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DR | CH87DR | ch8 7dr | ch87dr | Flintshire | Sir Y Fflint | Rhosesmor STW | 9384 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 317072 | 376669 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DS | CH87DS | ch8 7ds | ch87ds | Flintshire | Sir Y Fflint | Rhosesmor STW | 9194 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 317428 | 376619 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DT | CH87DT | ch8 7dt | ch87dt | Flintshire | Sir Y Fflint | Rhosesmor STW | 9094 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 317557 | 376564 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DU | CH87DU | ch8 7du | ch87du | Flintshire | Sir Y Fflint | Rhosesmor STW | 8361 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319485 | 376370 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DW | CH87DW | ch8 7dw | ch87dw | Flintshire | Sir Y Fflint | Rhosesmor STW | 9168 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 317528 | 376632 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DX | CH87DX | ch8 7dx | ch87dx | Flintshire | Sir Y Fflint | Rhosesmor STW | 8969 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 317752 | 376507 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DY | CH87DY | ch8 7dy | ch87dy | Flintshire | Sir Y Fflint | Rhosesmor STW | 9011 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 317684 | 376526 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7DZ | CH87DZ | ch8 7dz | ch87dz | Flintshire | Sir Y Fflint | Rhosesmor STW | 9103 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 317626 | 376602 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EA | CH87EA | ch8 7ea | ch87ea | Flintshire | Sir Y Fflint | Rhosesmor STW | 8293 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 319510 | 376305 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EB | CH87EB | ch8 7eb | ch87eb | Flintshire | Sir Y Fflint | Rhosesmor STW | 8237 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 319566 | 376259 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7ED | CH87ED | ch8 7ed | ch87ed | Flintshire | Sir Y Fflint | Rhosesmor STW | 8181 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 319512 | 376192 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EE | CH87EE | ch8 7ee | ch87ee | Flintshire | Sir Y Fflint | Rhosesmor STW | 9080 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 317730 | 376618 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EF | CH87EF | ch8 7ef | ch87ef | Flintshire | Sir Y Fflint | Rhosesmor STW | 9122 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 317720 | 376659 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EG | CH87EG | ch8 7eg | ch87eg | Flintshire | Sir Y Fflint | Rhosesmor STW | 8078 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 319766 | 376131 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EH | CH87EH | ch8 7eh | ch87eh | Flintshire | Sir Y Fflint | Rhosesmor STW | 8661 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 317924 | 376243 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EJ | CH87EJ | ch8 7ej | ch87ej | Flintshire | Sir Y Fflint | Rhosesmor STW | 9679 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 319567 | 377719 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EL | CH87EL | ch8 7el | ch87el | Flintshire | Sir Y Fflint | Rhosesmor STW | 9717 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 319633 | 377767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EN | CH87EN | ch8 7en | ch87en | Flintshire | Sir Y Fflint | Rhosesmor STW | 8211 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319107 | 376137 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EP | CH87EP | ch8 7ep | ch87ep | Flintshire | Sir Y Fflint | Rhosesmor STW | 9496 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 319770 | 377563 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EQ | CH87EQ | ch8 7eq | ch87eq | Flintshire | Sir Y Fflint | Rhosesmor STW | 8947 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 319908 | 377027 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7ER | CH87ER | ch8 7er | ch87er | Flintshire | Sir Y Fflint | Rhosesmor STW | 9426 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319125 | 377385 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7ES | CH87ES | ch8 7es | ch87es | Flintshire | Sir Y Fflint | Rhosesmor STW | 9641 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 319671 | 377696 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EU | CH87EU | ch8 7eu | ch87eu | Flintshire | Sir Y Fflint | Rhosesmor STW | 8925 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 319934 | 377008 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EW | CH87EW | ch8 7ew | ch87ew | Flintshire | Sir Y Fflint | Rhosesmor STW | 9349 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 319748 | 377412 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EX | CH87EX | ch8 7ex | ch87ex | Flintshire | Sir Y Fflint | Rhosesmor STW | 9255 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 319775 | 377321 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EY | CH87EY | ch8 7ey | ch87ey | Flintshire | Sir Y Fflint | Rhosesmor STW | 9131 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 319950 | 377217 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7EZ | CH87EZ | ch8 7ez | ch87ez | Flintshire | Sir Y Fflint | Rhosesmor STW | 7819 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 319822 | 375877 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7FA | CH87FA | ch8 7fa | ch87fa | Flintshire | Sir Y Fflint | Rhosesmor STW | 8553 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320375 | 376677 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7FB | CH87FB | ch8 7fb | ch87fb | Flintshire | Sir Y Fflint | Rhosesmor STW | 8985 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 317858 | 376565 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7FD | CH87FD | ch8 7fd | ch87fd | Flintshire | Sir Y Fflint | Rhosesmor STW | 7977 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318653 | 375771 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7FE | CH87FE | ch8 7fe | ch87fe | Flintshire | Sir Y Fflint | Rhosesmor STW | 7969 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318626 | 375754 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7FF | CH87FF | ch8 7ff | ch87ff | Flintshire | Sir Y Fflint | Rhosesmor STW | 9122 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320121 | 377227 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7FH | CH87FH | ch8 7fh | ch87fh | Flintshire | Sir Y Fflint | Rhosesmor STW | 9260 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319204 | 377231 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7FJ | CH87FJ | ch8 7fj | ch87fj | Flintshire | Sir Y Fflint | Rhosesmor STW | 7949 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318698 | 375756 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7FL | CH87FL | ch8 7fl | ch87fl | Flintshire | Sir Y Fflint | Rhosesmor STW | 7063 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318968 | 374912 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7FP | CH87FP | ch8 7fp | ch87fp | Flintshire | Sir Y Fflint | Rhosesmor STW | 8937 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320082 | 377037 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7GA | CH87GA | ch8 7ga | ch87ga | Flintshire | Sir Y Fflint | Rhosesmor STW | 7666 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318895 | 375519 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7GB | CH87GB | ch8 7gb | ch87gb | Flintshire | Sir Y Fflint | Rhosesmor STW | 8326 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318569 | 376110 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7GD | CH87GD | ch8 7gd | ch87gd | Flintshire | Sir Y Fflint | Rhosesmor STW | 9430 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319307 | 377424 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7GH | CH87GH | ch8 7gh | ch87gh | Flintshire | Sir Y Fflint | Rhosesmor STW | 9402 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 319510 | 377430 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7GJ | CH87GJ | ch8 7gj | ch87gj | Flintshire | Sir Y Fflint | Rhosesmor STW | 9609 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 319977 | 377701 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7GR | CH87GR | ch8 7gr | ch87gr | Flintshire | Sir Y Fflint | Rhosesmor STW | 9527 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 319528 | 377560 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HA | CH87HA | ch8 7ha | ch87ha | Flintshire | Sir Y Fflint | Rhosesmor STW | 8139 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 319749 | 376190 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HB | CH87HB | ch8 7hb | ch87hb | Flintshire | Sir Y Fflint | Rhosesmor STW | 8200 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 319715 | 376246 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HD | CH87HD | ch8 7hd | ch87hd | Flintshire | Sir Y Fflint | Rhosesmor STW | 8954 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320030 | 377048 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HE | CH87HE | ch8 7he | ch87he | Flintshire | Sir Y Fflint | Rhosesmor STW | 8912 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 319995 | 377002 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HF | CH87HF | ch8 7hf | ch87hf | Flintshire | Sir Y Fflint | Rhosesmor STW | 8953 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320146 | 377059 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HG | CH87HG | ch8 7hg | ch87hg | Flintshire | Sir Y Fflint | Rhosesmor STW | 8734 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320304 | 376853 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HH | CH87HH | ch8 7hh | ch87hh | Flintshire | Sir Y Fflint | Rhosesmor STW | 8277 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 320080 | 376373 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HJ | CH87HJ | ch8 7hj | ch87hj | Flintshire | Sir Y Fflint | Rhosesmor STW | 9387 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 319912 | 377471 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HL | CH87HL | ch8 7hl | ch87hl | Flintshire | Sir Y Fflint | Rhosesmor STW | 8046 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 319714 | 376090 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HN | CH87HN | ch8 7hn | ch87hn | Flintshire | Sir Y Fflint | Rhosesmor STW | 8023 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318792 | 375861 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HP | CH87HP | ch8 7hp | ch87hp | Flintshire | Sir Y Fflint | Rhosesmor STW | 8258 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 319688 | 376300 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HQ | CH87HQ | ch8 7hq | ch87hq | Flintshire | Sir Y Fflint | Rhosesmor STW | 8693 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320260 | 376809 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HR | CH87HR | ch8 7hr | ch87hr | Flintshire | Sir Y Fflint | Rhosesmor STW | 9444 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319197 | 377417 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HS | CH87HS | ch8 7hs | ch87hs | Flintshire | Sir Y Fflint | Rhosesmor STW | 9490 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319076 | 377440 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HT | CH87HT | ch8 7ht | ch87ht | Flintshire | Sir Y Fflint | Rhosesmor STW | 9640 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319010 | 377579 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HU | CH87HU | ch8 7hu | ch87hu | Flintshire | Sir Y Fflint | Rhosesmor STW | 8291 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 319681 | 376333 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HW | CH87HW | ch8 7hw | ch87hw | Flintshire | Sir Y Fflint | Rhosesmor STW | 9074 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320053 | 377172 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HX | CH87HX | ch8 7hx | ch87hx | Flintshire | Sir Y Fflint | Rhosesmor STW | 8147 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 319520 | 376159 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HY | CH87HY | ch8 7hy | ch87hy | Flintshire | Sir Y Fflint | Rhosesmor STW | 9364 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319081 | 377312 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7HZ | CH87HZ | ch8 7hz | ch87hz | Flintshire | Sir Y Fflint | Rhosesmor STW | 9449 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318928 | 377366 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JA | CH87JA | ch8 7ja | ch87ja | Flintshire | Sir Y Fflint | Rhosesmor STW | 8202 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318411 | 375930 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JB | CH87JB | ch8 7jb | ch87jb | Flintshire | Sir Y Fflint | Rhosesmor STW | 9417 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318984 | 377346 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JD | CH87JD | ch8 7jd | ch87jd | Flintshire | Sir Y Fflint | Rhosesmor STW | 9422 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319039 | 377363 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JE | CH87JE | ch8 7je | ch87je | Flintshire | Sir Y Fflint | Rhosesmor STW | 9699 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319028 | 377643 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JF | CH87JF | ch8 7jf | ch87jf | Flintshire | Sir Y Fflint | Rhosesmor STW | 9643 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319060 | 377593 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JG | CH87JG | ch8 7jg | ch87jg | Flintshire | Sir Y Fflint | Rhosesmor STW | 9687 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319176 | 377661 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JH | CH87JH | ch8 7jh | ch87jh | Flintshire | Sir Y Fflint | Rhosesmor STW | 9470 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319065 | 377417 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JJ | CH87JJ | ch8 7jj | ch87jj | Flintshire | Sir Y Fflint | Rhosesmor STW | 9675 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319137 | 377641 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JL | CH87JL | ch8 7jl | ch87jl | Flintshire | Sir Y Fflint | Rhosesmor STW | 8159 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318418 | 375887 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JN | CH87JN | ch8 7jn | ch87jn | Flintshire | Sir Y Fflint | Rhosesmor STW | 9619 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319241 | 377604 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JP | CH87JP | ch8 7jp | ch87jp | Flintshire | Sir Y Fflint | Rhosesmor STW | 9523 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319256 | 377509 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JQ | CH87JQ | ch8 7jq | ch87jq | Flintshire | Sir Y Fflint | Rhosesmor STW | 9818 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319111 | 377781 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JR | CH87JR | ch8 7jr | ch87jr | Flintshire | Sir Y Fflint | Rhosesmor STW | 9611 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319291 | 377605 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JS | CH87JS | ch8 7js | ch87js | Flintshire | Sir Y Fflint | Rhosesmor STW | 8734 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320447 | 376864 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JT | CH87JT | ch8 7jt | ch87jt | Flintshire | Sir Y Fflint | Rhosesmor STW | 9662 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319329 | 377663 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JU | CH87JU | ch8 7ju | ch87ju | Flintshire | Sir Y Fflint | Rhosesmor STW | 9721 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319368 | 377730 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JW | CH87JW | ch8 7jw | ch87jw | Flintshire | Sir Y Fflint | Rhosesmor STW | 9605 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319185 | 377579 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JX | CH87JX | ch8 7jx | ch87jx | Flintshire | Sir Y Fflint | Rhosesmor STW | 9519 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319189 | 377492 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JY | CH87JY | ch8 7jy | ch87jy | Flintshire | Sir Y Fflint | Rhosesmor STW | 9565 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319324 | 377564 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7JZ | CH87JZ | ch8 7jz | ch87jz | Flintshire | Sir Y Fflint | Rhosesmor STW | 9511 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319331 | 377510 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LA | CH87LA | ch8 7la | ch87la | Flintshire | Sir Y Fflint | Rhosesmor STW | 8184 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318571 | 375963 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LB | CH87LB | ch8 7lb | ch87lb | Flintshire | Sir Y Fflint | Rhosesmor STW | 8826 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320171 | 376934 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LD | CH87LD | ch8 7ld | ch87ld | Flintshire | Sir Y Fflint | Rhosesmor STW | 8020 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318611 | 375803 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LE | CH87LE | ch8 7le | ch87le | Flintshire | Sir Y Fflint | Rhosesmor STW | 8016 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318661 | 375814 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LF | CH87LF | ch8 7lf | ch87lf | Flintshire | Sir Y Fflint | Rhosesmor STW | 8813 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320121 | 376916 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LG | CH87LG | ch8 7lg | ch87lg | Flintshire | Sir Y Fflint | Rhosesmor STW | 9060 | 890 | 700to900 | 1.78 | 1.3 | 0.96 | 16.59 | 8.85 | 9.78 | 317425 | 376472 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LH | CH87LH | ch8 7lh | ch87lh | Flintshire | Sir Y Fflint | Rhosesmor STW | 8091 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318590 | 375871 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LL | CH87LL | ch8 7ll | ch87ll | Flintshire | Sir Y Fflint | Rhosesmor STW | 7984 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318677 | 375786 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LP | CH87LP | ch8 7lp | ch87lp | Flintshire | Sir Y Fflint | Rhosesmor STW | 8189 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318508 | 375948 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LQ | CH87LQ | ch8 7lq | ch87lq | Flintshire | Sir Y Fflint | Rhosesmor STW | 9160 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 317344 | 376546 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LR | CH87LR | ch8 7lr | ch87lr | Flintshire | Sir Y Fflint | Rhosesmor STW | 8189 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318368 | 375902 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LS | CH87LS | ch8 7ls | ch87ls | Flintshire | Sir Y Fflint | Rhosesmor STW | 8356 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318484 | 376115 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LU | CH87LU | ch8 7lu | ch87lu | Flintshire | Sir Y Fflint | Rhosesmor STW | 8109 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318427 | 375837 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LW | CH87LW | ch8 7lw | ch87lw | Flintshire | Sir Y Fflint | Rhosesmor STW | 8156 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318447 | 375893 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7LY | CH87LY | ch8 7ly | ch87ly | Flintshire | Sir Y Fflint | Rhosesmor STW | 8326 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318456 | 376075 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NA | CH87NA | ch8 7na | ch87na | Flintshire | Sir Y Fflint | Rhosesmor STW | 9132 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 317420 | 376548 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NB | CH87NB | ch8 7nb | ch87nb | Flintshire | Sir Y Fflint | Rhosesmor STW | 8389 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318469 | 376145 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7ND | CH87ND | ch8 7nd | ch87nd | Flintshire | Sir Y Fflint | Rhosesmor STW | 8276 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318391 | 376001 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NE | CH87NE | ch8 7ne | ch87ne | Flintshire | Sir Y Fflint | Rhosesmor STW | 8265 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318453 | 376010 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NF | CH87NF | ch8 7nf | ch87nf | Flintshire | Sir Y Fflint | Rhosesmor STW | 8291 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318295 | 375985 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NG | CH87NG | ch8 7ng | ch87ng | Flintshire | Sir Y Fflint | Rhosesmor STW | 8309 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318261 | 375992 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NH | CH87NH | ch8 7nh | ch87nh | Flintshire | Sir Y Fflint | Rhosesmor STW | 9008 | 890 | 700to900 | 1.78 | 1.3 | 0.96 | 16.59 | 8.85 | 9.78 | 317490 | 376443 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NJ | CH87NJ | ch8 7nj | ch87nj | Flintshire | Sir Y Fflint | Rhosesmor STW | 8370 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318314 | 376075 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NL | CH87NL | ch8 7nl | ch87nl | Flintshire | Sir Y Fflint | Rhosesmor STW | 8267 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318336 | 375973 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NN | CH87NN | ch8 7nn | ch87nn | Flintshire | Sir Y Fflint | Rhosesmor STW | 8800 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 317839 | 376360 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NP | CH87NP | ch8 7np | ch87np | Flintshire | Sir Y Fflint | Rhosesmor STW | 8927 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 317607 | 376404 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NQ | CH87NQ | ch8 7nq | ch87nq | Flintshire | Sir Y Fflint | Rhosesmor STW | 8885 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 317683 | 376390 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NR | CH87NR | ch8 7nr | ch87nr | Flintshire | Sir Y Fflint | Rhosesmor STW | 9005 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 317523 | 376454 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NS | CH87NS | ch8 7ns | ch87ns | Flintshire | Sir Y Fflint | Rhosesmor STW | 8869 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 317734 | 376393 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NT | CH87NT | ch8 7nt | ch87nt | Flintshire | Sir Y Fflint | Rhosesmor STW | 8743 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 317922 | 376330 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NW | CH87NW | ch8 7nw | ch87nw | Flintshire | Sir Y Fflint | Rhosesmor STW | 8753 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 317828 | 376305 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NX | CH87NX | ch8 7nx | ch87nx | Flintshire | Sir Y Fflint | Rhosesmor STW | 9127 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319075 | 377069 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NY | CH87NY | ch8 7ny | ch87ny | Flintshire | Sir Y Fflint | Rhosesmor STW | 8477 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 317979 | 376068 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7NZ | CH87NZ | ch8 7nz | ch87nz | Flintshire | Sir Y Fflint | Rhosesmor STW | 8408 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318097 | 376038 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PA | CH87PA | ch8 7pa | ch87pa | Flintshire | Sir Y Fflint | Rhosesmor STW | 9303 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 317420 | 376733 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PB | CH87PB | ch8 7pb | ch87pb | Flintshire | Sir Y Fflint | Rhosesmor STW | 8630 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 320414 | 376757 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PD | CH87PD | ch8 7pd | ch87pd | Flintshire | Sir Y Fflint | Rhosesmor STW | 8176 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318786 | 376018 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PE | CH87PE | ch8 7pe | ch87pe | Flintshire | Sir Y Fflint | Rhosesmor STW | 8290 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318808 | 376142 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PF | CH87PF | ch8 7pf | ch87pf | Flintshire | Sir Y Fflint | Rhosesmor STW | 8210 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318806 | 376059 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PG | CH87PG | ch8 7pg | ch87pg | Flintshire | Sir Y Fflint | Rhosesmor STW | 9301 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 317470 | 376752 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PH | CH87PH | ch8 7ph | ch87ph | Flintshire | Sir Y Fflint | Rhosesmor STW | 8233 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318826 | 376088 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PJ | CH87PJ | ch8 7pj | ch87pj | Flintshire | Sir Y Fflint | Rhosesmor STW | 8343 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318709 | 376169 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PL | CH87PL | ch8 7pl | ch87pl | Flintshire | Sir Y Fflint | Rhosesmor STW | 8265 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318560 | 376044 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PN | CH87PN | ch8 7pn | ch87pn | Flintshire | Sir Y Fflint | Rhosesmor STW | 8567 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318546 | 376355 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PP | CH87PP | ch8 7pp | ch87pp | Flintshire | Sir Y Fflint | Rhosesmor STW | 8395 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318534 | 376172 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PQ | CH87PQ | ch8 7pq | ch87pq | Flintshire | Sir Y Fflint | Rhosesmor STW | 8199 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318564 | 375976 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PR | CH87PR | ch8 7pr | ch87pr | Flintshire | Sir Y Fflint | Rhosesmor STW | 9306 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318773 | 377183 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PS | CH87PS | ch8 7ps | ch87ps | Flintshire | Sir Y Fflint | Rhosesmor STW | 9008 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318965 | 376922 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PT | CH87PT | ch8 7pt | ch87pt | Flintshire | Sir Y Fflint | Rhosesmor STW | 9277 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318834 | 377168 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PU | CH87PU | ch8 7pu | ch87pu | Flintshire | Sir Y Fflint | Rhosesmor STW | 9207 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318734 | 377071 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PW | CH87PW | ch8 7pw | ch87pw | Flintshire | Sir Y Fflint | Rhosesmor STW | 9339 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318824 | 377229 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PX | CH87PX | ch8 7px | ch87px | Flintshire | Sir Y Fflint | Rhosesmor STW | 8743 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318687 | 376579 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PY | CH87PY | ch8 7py | ch87py | Flintshire | Sir Y Fflint | Rhosesmor STW | 8782 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318748 | 376635 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7PZ | CH87PZ | ch8 7pz | ch87pz | Flintshire | Sir Y Fflint | Rhosesmor STW | 8764 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318736 | 376614 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QA | CH87QA | ch8 7qa | ch87qa | Flintshire | Sir Y Fflint | Rhosesmor STW | 9182 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318848 | 377073 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QB | CH87QB | ch8 7qb | ch87qb | Flintshire | Sir Y Fflint | Rhosesmor STW | 9189 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319124 | 377142 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QD | CH87QD | ch8 7qd | ch87qd | Flintshire | Sir Y Fflint | Rhosesmor STW | 8800 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318778 | 376662 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QE | CH87QE | ch8 7qe | ch87qe | Flintshire | Sir Y Fflint | Rhosesmor STW | 8823 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318749 | 376678 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QF | CH87QF | ch8 7qf | ch87qf | Flintshire | Sir Y Fflint | Rhosesmor STW | 8904 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318843 | 376786 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QG | CH87QG | ch8 7qg | ch87qg | Flintshire | Sir Y Fflint | Rhosesmor STW | 8930 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318934 | 376835 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QH | CH87QH | ch8 7qh | ch87qh | Flintshire | Sir Y Fflint | Rhosesmor STW | 9076 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319027 | 377006 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QJ | CH87QJ | ch8 7qj | ch87qj | Flintshire | Sir Y Fflint | Rhosesmor STW | 9088 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319073 | 377028 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QL | CH87QL | ch8 7ql | ch87ql | Flintshire | Sir Y Fflint | Rhosesmor STW | 9152 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319081 | 377096 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QN | CH87QN | ch8 7qn | ch87qn | Flintshire | Sir Y Fflint | Rhosesmor STW | 9404 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319167 | 377371 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QP | CH87QP | ch8 7qp | ch87qp | Flintshire | Sir Y Fflint | Rhosesmor STW | 9217 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319156 | 377178 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QQ | CH87QQ | ch8 7qq | ch87qq | Flintshire | Sir Y Fflint | Rhosesmor STW | 9210 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318996 | 377136 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QR | CH87QR | ch8 7qr | ch87qr | Flintshire | Sir Y Fflint | Rhosesmor STW | 9323 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319105 | 377275 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QS | CH87QS | ch8 7qs | ch87qs | Flintshire | Sir Y Fflint | Rhosesmor STW | 9544 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319406 | 377557 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QT | CH87QT | ch8 7qt | ch87qt | Flintshire | Sir Y Fflint | Rhosesmor STW | 9646 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319479 | 377672 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QU | CH87QU | ch8 7qu | ch87qu | Flintshire | Sir Y Fflint | Rhosesmor STW | 9438 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319369 | 377443 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QW | CH87QW | ch8 7qw | ch87qw | Flintshire | Sir Y Fflint | Rhosesmor STW | 9264 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318662 | 377111 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QX | CH87QX | ch8 7qx | ch87qx | Flintshire | Sir Y Fflint | Rhosesmor STW | 9483 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319357 | 377486 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QY | CH87QY | ch8 7qy | ch87qy | Flintshire | Sir Y Fflint | Rhosesmor STW | 8276 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318306 | 375972 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7QZ | CH87QZ | ch8 7qz | ch87qz | Flintshire | Sir Y Fflint | Rhosesmor STW | 9193 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318925 | 377103 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RA | CH87RA | ch8 7ra | ch87ra | Flintshire | Sir Y Fflint | Rhosesmor STW | 7802 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318683 | 375597 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RD | CH87RD | ch8 7rd | ch87rd | Flintshire | Sir Y Fflint | Rhosesmor STW | 7818 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318743 | 375632 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RE | CH87RE | ch8 7re | ch87re | Flintshire | Sir Y Fflint | Rhosesmor STW | 7873 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318726 | 375685 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RF | CH87RF | ch8 7rf | ch87rf | Flintshire | Sir Y Fflint | Rhosesmor STW | 8737 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318733 | 376585 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RG | CH87RG | ch8 7rg | ch87rg | Flintshire | Sir Y Fflint | Rhosesmor STW | 7275 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318871 | 375104 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RH | CH87RH | ch8 7rh | ch87rh | Flintshire | Sir Y Fflint | Rhosesmor STW | 7287 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318946 | 375139 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RJ | CH87RJ | ch8 7rj | ch87rj | Flintshire | Sir Y Fflint | Rhosesmor STW | 7384 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318849 | 375211 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RL | CH87RL | ch8 7rl | ch87rl | Flintshire | Sir Y Fflint | Rhosesmor STW | 7332 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318864 | 375162 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RN | CH87RN | ch8 7rn | ch87rn | Flintshire | Sir Y Fflint | Rhosesmor STW | 7273 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318975 | 375133 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RP | CH87RP | ch8 7rp | ch87rp | Flintshire | Sir Y Fflint | Rhosesmor STW | 7497 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318768 | 375305 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RQ | CH87RQ | ch8 7rq | ch87rq | Flintshire | Sir Y Fflint | Rhosesmor STW | 8415 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318560 | 376201 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RS | CH87RS | ch8 7rs | ch87rs | Flintshire | Sir Y Fflint | Rhosesmor STW | 7918 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318817 | 375758 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RU | CH87RU | ch8 7ru | ch87ru | Flintshire | Sir Y Fflint | Rhosesmor STW | 9267 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 319147 | 377227 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RX | CH87RX | ch8 7rx | ch87rx | Flintshire | Sir Y Fflint | Rhosesmor STW | 7403 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318895 | 375245 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RY | CH87RY | ch8 7ry | ch87ry | Flintshire | Sir Y Fflint | Rhosesmor STW | 7251 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318929 | 375097 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7RZ | CH87RZ | ch8 7rz | ch87rz | Flintshire | Sir Y Fflint | Rhosesmor STW | 7140 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318989 | 374999 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SA | CH87SA | ch8 7sa | ch87sa | Flintshire | Sir Y Fflint | Rhosesmor STW | 7207 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318932 | 375051 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SB | CH87SB | ch8 7sb | ch87sb | Flintshire | Sir Y Fflint | Rhosesmor STW | 6766 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 319171 | 374662 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SD | CH87SD | ch8 7sd | ch87sd | Flintshire | Sir Y Fflint | Rhosesmor STW | 8145 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318299 | 375831 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SE | CH87SE | ch8 7se | ch87se | Flintshire | Sir Y Fflint | Rhosesmor STW | 6689 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 319188 | 374587 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SF | CH87SF | ch8 7sf | ch87sf | Flintshire | Sir Y Fflint | Rhosesmor STW | 6705 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 319108 | 374580 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SG | CH87SG | ch8 7sg | ch87sg | Flintshire | Sir Y Fflint | Rhosesmor STW | 7162 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 319008 | 375027 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SH | CH87SH | ch8 7sh | ch87sh | Flintshire | Sir Y Fflint | Rhosesmor STW | 6666 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 319104 | 374538 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SJ | CH87SJ | ch8 7sj | ch87sj | Flintshire | Sir Y Fflint | Rhosesmor STW | 6718 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 319337 | 374657 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SL | CH87SL | ch8 7sl | ch87sl | Flintshire | Sir Y Fflint | Rhosesmor STW | 7717 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318866 | 375564 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SN | CH87SN | ch8 7sn | ch87sn | Flintshire | Sir Y Fflint | Rhosesmor STW | 6754 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318978 | 374592 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SP | CH87SP | ch8 7sp | ch87sp | Flintshire | Sir Y Fflint | Rhosesmor STW | 7418 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318935 | 375272 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SQ | CH87SQ | ch8 7sq | ch87sq | Flintshire | Sir Y Fflint | Rhosesmor STW | 7162 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318923 | 375002 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SR | CH87SR | ch8 7sr | ch87sr | Flintshire | Sir Y Fflint | Rhosesmor STW | 8148 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318580 | 375928 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SW | CH87SW | ch8 7sw | ch87sw | Flintshire | Sir Y Fflint | Rhosesmor STW | 6922 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318978 | 374768 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SX | CH87SX | ch8 7sx | ch87sx | Flintshire | Sir Y Fflint | Rhosesmor STW | 6723 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318900 | 374534 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7SY | CH87SY | ch8 7sy | ch87sy | Flintshire | Sir Y Fflint | Rhosesmor STW | 6812 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318913 | 374632 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TD | CH87TD | ch8 7td | ch87td | Flintshire | Sir Y Fflint | Rhosesmor STW | 8185 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318557 | 375959 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TE | CH87TE | ch8 7te | ch87te | Flintshire | Sir Y Fflint | Rhosesmor STW | 8112 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318620 | 375902 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TF | CH87TF | ch8 7tf | ch87tf | Flintshire | Sir Y Fflint | Rhosesmor STW | 7999 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318698 | 375808 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TG | CH87TG | ch8 7tg | ch87tg | Flintshire | Sir Y Fflint | Rhosesmor STW | 8086 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318641 | 375882 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TH | CH87TH | ch8 7th | ch87th | Flintshire | Sir Y Fflint | Rhosesmor STW | 7941 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318656 | 375735 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TJ | CH87TJ | ch8 7tj | ch87tj | Flintshire | Sir Y Fflint | Rhosesmor STW | 8124 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318658 | 375926 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TL | CH87TL | ch8 7tl | ch87tl | Flintshire | Sir Y Fflint | Rhosesmor STW | 7892 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318996 | 375781 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TN | CH87TN | ch8 7tn | ch87tn | Flintshire | Sir Y Fflint | Rhosesmor STW | 7966 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318675 | 375767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TQ | CH87TQ | ch8 7tq | ch87tq | Flintshire | Sir Y Fflint | Rhosesmor STW | 8035 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318502 | 375784 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TR | CH87TR | ch8 7tr | ch87tr | Flintshire | Sir Y Fflint | Rhosesmor STW | 7990 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318722 | 375806 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TS | CH87TS | ch8 7ts | ch87ts | Flintshire | Sir Y Fflint | Rhosesmor STW | 7986 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318895 | 375851 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TW | CH87TW | ch8 7tw | ch87tw | Flintshire | Sir Y Fflint | Rhosesmor STW | 7946 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318736 | 375764 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TX | CH87TX | ch8 7tx | ch87tx | Flintshire | Sir Y Fflint | Rhosesmor STW | 7841 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318805 | 375675 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7TZ | CH87TZ | ch8 7tz | ch87tz | Flintshire | Sir Y Fflint | Rhosesmor STW | 7547 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318898 | 375396 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UA | CH87UA | ch8 7ua | ch87ua | Flintshire | Sir Y Fflint | Rhosesmor STW | 7747 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319116 | 375662 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UB | CH87UB | ch8 7ub | ch87ub | Flintshire | Sir Y Fflint | Rhosesmor STW | 8148 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318580 | 375928 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UD | CH87UD | ch8 7ud | ch87ud | Flintshire | Sir Y Fflint | Rhosesmor STW | 7581 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318856 | 375419 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UF | CH87UF | ch8 7uf | ch87uf | Flintshire | Sir Y Fflint | Rhosesmor STW | 7663 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318843 | 375501 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UG | CH87UG | ch8 7ug | ch87ug | Flintshire | Sir Y Fflint | Rhosesmor STW | 8073 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318438 | 375803 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UH | CH87UH | ch8 7uh | ch87uh | Flintshire | Sir Y Fflint | Rhosesmor STW | 8059 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318892 | 375926 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UJ | CH87UJ | ch8 7uj | ch87uj | Flintshire | Sir Y Fflint | Rhosesmor STW | 8214 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318150 | 375851 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UL | CH87UL | ch8 7ul | ch87ul | Flintshire | Sir Y Fflint | Rhosesmor STW | 8002 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318851 | 375855 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UN | CH87UN | ch8 7un | ch87un | Flintshire | Sir Y Fflint | Rhosesmor STW | 7757 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318905 | 375616 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UP | CH87UP | ch8 7up | ch87up | Flintshire | Sir Y Fflint | Rhosesmor STW | 7857 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318846 | 375703 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UQ | CH87UQ | ch8 7uq | ch87uq | Flintshire | Sir Y Fflint | Rhosesmor STW | 8299 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318184 | 375954 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UR | CH87UR | ch8 7ur | ch87ur | Flintshire | Sir Y Fflint | Rhosesmor STW | 7840 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318651 | 375627 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7US | CH87US | ch8 7us | ch87us | Flintshire | Sir Y Fflint | Rhosesmor STW | 7693 | 888 | 700to900 | 1.78 | 1.3 | 0.95 | 16.55 | 8.83 | 9.76 | 318708 | 375491 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UT | CH87UT | ch8 7ut | ch87ut | Flintshire | Sir Y Fflint | Rhosesmor STW | 7862 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318488 | 375597 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UU | CH87UU | ch8 7uu | ch87uu | Flintshire | Sir Y Fflint | Rhosesmor STW | 7770 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318671 | 375560 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UW | CH87UW | ch8 7uw | ch87uw | Flintshire | Sir Y Fflint | Rhosesmor STW | 7760 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 319005 | 375647 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UX | CH87UX | ch8 7ux | ch87ux | Flintshire | Sir Y Fflint | Rhosesmor STW | 8025 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318420 | 375746 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UY | CH87UY | ch8 7uy | ch87uy | Flintshire | Sir Y Fflint | Rhosesmor STW | 8118 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318357 | 375823 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7UZ | CH87UZ | ch8 7uz | ch87uz | Flintshire | Sir Y Fflint | Rhosesmor STW | 8022 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318475 | 375762 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7WJ | CH87WJ | ch8 7wj | ch87wj | Flintshire | Sir Y Fflint | Rhosesmor STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323909 | 372767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7XE | CH87XE | ch8 7xe | ch87xe | Flintshire | Sir Y Fflint | Rhosesmor STW | 9428 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 317450 | 376881 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7XF | CH87XF | ch8 7xf | ch87xf | Flintshire | Sir Y Fflint | Rhosesmor STW | 7897 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318797 | 375731 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7XG | CH87XG | ch8 7xg | ch87xg | Flintshire | Sir Y Fflint | Rhosesmor STW | 7874 | 850 | 700to900 | 1.7 | 1.24 | 0.91 | 15.84 | 8.45 | 9.34 | 318784 | 375703 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7XL | CH87XL | ch8 7xl | ch87xl | Flintshire | Sir Y Fflint | Rhosesmor STW | 9148 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318838 | 377036 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7XP | CH87XP | ch8 7xp | ch87xp | Flintshire | Sir Y Fflint | Rhosesmor STW | 9323 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318746 | 377193 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7XW | CH87XW | ch8 7xw | ch87xw | Flintshire | Sir Y Fflint | Rhosesmor STW | 9222 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 318763 | 377094 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 7XX | CH87XX | ch8 7xx | ch87xx | Flintshire | Sir Y Fflint | Rhosesmor STW | 9646 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319447 | 377667 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8AN | CH88AN | ch8 8an | ch88an | Flintshire | Sir Y Fflint | Rhosesmor STW | 4649 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 319903 | 372666 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8AR | CH88AR | ch8 8ar | ch88ar | Flintshire | Sir Y Fflint | Rhosesmor STW | 4704 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 319956 | 372735 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8AT | CH88AT | ch8 8at | ch88at | Flintshire | Sir Y Fflint | Rhosesmor STW | 5624 | 924 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.22 | 9.19 | 10.15 | 319070 | 373431 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8AU | CH88AU | ch8 8au | ch88au | Flintshire | Sir Y Fflint | Rhosesmor STW | 4672 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 319808 | 372666 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8AW | CH88AW | ch8 8aw | ch88aw | Flintshire | Sir Y Fflint | Rhosesmor STW | 4660 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 319847 | 372664 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8AX | CH88AX | ch8 8ax | ch88ax | Flintshire | Sir Y Fflint | Rhosesmor STW | 6639 | 914 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.04 | 9.09 | 10.04 | 318466 | 374284 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8AZ | CH88AZ | ch8 8az | ch88az | Flintshire | Sir Y Fflint | Rhosesmor STW | 9726 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316226 | 376620 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8BA | CH88BA | ch8 8ba | ch88ba | Flintshire | Sir Y Fflint | Rhosesmor STW | 4219 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320313 | 372311 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8BB | CH88BB | ch8 8bb | ch88bb | Flintshire | Sir Y Fflint | Rhosesmor STW | 5906 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 318786 | 373623 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8BD | CH88BD | ch8 8bd | ch88bd | Flintshire | Sir Y Fflint | Rhosesmor STW | 4761 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 320736 | 372902 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8BE | CH88BE | ch8 8be | ch88be | Flintshire | Sir Y Fflint | Rhosesmor STW | 5968 | 886 | 700to900 | 1.77 | 1.3 | 0.95 | 16.51 | 8.81 | 9.73 | 319783 | 373991 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8BH | CH88BH | ch8 8bh | ch88bh | Flintshire | Sir Y Fflint | Rhosesmor STW | 9845 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316551 | 376929 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8BS | CH88BS | ch8 8bs | ch88bs | Flintshire | Sir Y Fflint | Rhosesmor STW | 3625 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 320575 | 371749 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8BT | CH88BT | ch8 8bt | ch88bt | Flintshire | Sir Y Fflint | Rhosesmor STW | 3307 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320643 | 371437 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8BU | CH88BU | ch8 8bu | ch88bu | Flintshire | Sir Y Fflint | Rhosesmor STW | 3013 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320861 | 371159 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8BX | CH88BX | ch8 8bx | ch88bx | Flintshire | Sir Y Fflint | Rhosesmor STW | 2767 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320944 | 370916 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8BY | CH88BY | ch8 8by | ch88by | Flintshire | Sir Y Fflint | Rhosesmor STW | 2965 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 321121 | 371112 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8BZ | CH88BZ | ch8 8bz | ch88bz | Flintshire | Sir Y Fflint | Rhosesmor STW | 2967 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 321183 | 371110 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DD | CH88DD | ch8 8dd | ch88dd | Flintshire | Sir Y Fflint | Rhosesmor STW | 3509 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 321479 | 371625 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DE | CH88DE | ch8 8de | ch88de | Flintshire | Sir Y Fflint | Rhosesmor STW | 3566 | 863 | 700to900 | 1.73 | 1.26 | 0.93 | 16.08 | 8.58 | 9.48 | 321863 | 371609 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DF | CH88DF | ch8 8df | ch88df | Flintshire | Sir Y Fflint | Rhosesmor STW | 2508 | 867 | 700to900 | 1.74 | 1.27 | 0.93 | 16.16 | 8.62 | 9.53 | 321670 | 370566 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DH | CH88DH | ch8 8dh | ch88dh | Flintshire | Sir Y Fflint | Rhosesmor STW | 1816 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 321173 | 369957 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DJ | CH88DJ | ch8 8dj | ch88dj | Flintshire | Sir Y Fflint | Rhosesmor STW | 1827 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 320998 | 369976 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DL | CH88DL | ch8 8dl | ch88dl | Flintshire | Sir Y Fflint | Rhosesmor STW | 2309 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 320901 | 370456 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DP | CH88DP | ch8 8dp | ch88dp | Flintshire | Sir Y Fflint | Rhosesmor STW | 2109 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 320899 | 370256 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DR | CH88DR | ch8 8dr | ch88dr | Flintshire | Sir Y Fflint | Rhosesmor STW | 2448 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320895 | 370595 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DT | CH88DT | ch8 8dt | ch88dt | Flintshire | Sir Y Fflint | Rhosesmor STW | 2148 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 320875 | 370294 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DU | CH88DU | ch8 8du | ch88du | Flintshire | Sir Y Fflint | Rhosesmor STW | 2436 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320670 | 370563 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DX | CH88DX | ch8 8dx | ch88dx | Flintshire | Sir Y Fflint | Rhosesmor STW | 2508 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320763 | 370646 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DY | CH88DY | ch8 8dy | ch88dy | Flintshire | Sir Y Fflint | Rhosesmor STW | 2262 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 320860 | 370407 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8DZ | CH88DZ | ch8 8dz | ch88dz | Flintshire | Sir Y Fflint | Rhosesmor STW | 2425 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320785 | 370565 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8EA | CH88EA | ch8 8ea | ch88ea | Flintshire | Sir Y Fflint | Rhosesmor STW | 2598 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320663 | 370725 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8EE | CH88EE | ch8 8ee | ch88ee | Flintshire | Sir Y Fflint | Rhosesmor STW | 2592 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320579 | 370707 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8EF | CH88EF | ch8 8ef | ch88ef | Flintshire | Sir Y Fflint | Rhosesmor STW | 2465 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320667 | 370592 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8EG | CH88EG | ch8 8eg | ch88eg | Flintshire | Sir Y Fflint | Rhosesmor STW | 2377 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320670 | 370503 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8EH | CH88EH | ch8 8eh | ch88eh | Flintshire | Sir Y Fflint | Rhosesmor STW | 2672 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320773 | 370811 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8EJ | CH88EJ | ch8 8ej | ch88ej | Flintshire | Sir Y Fflint | Rhosesmor STW | 2743 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320673 | 370873 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8EQ | CH88EQ | ch8 8eq | ch88eq | Flintshire | Sir Y Fflint | Rhosesmor STW | 2310 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 320642 | 370431 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8ES | CH88ES | ch8 8es | ch88es | Flintshire | Sir Y Fflint | Rhosesmor STW | 2564 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320763 | 370702 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8EU | CH88EU | ch8 8eu | ch88eu | Flintshire | Sir Y Fflint | Rhosesmor STW | 3549 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320018 | 371559 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8EW | CH88EW | ch8 8ew | ch88ew | Flintshire | Sir Y Fflint | Rhosesmor STW | 2771 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 320532 | 370880 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8EX | CH88EX | ch8 8ex | ch88ex | Flintshire | Sir Y Fflint | Rhosesmor STW | 3762 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320016 | 371780 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HA | CH88HA | ch8 8ha | ch88ha | Flintshire | Sir Y Fflint | Rhosesmor STW | 3976 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320293 | 372061 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HB | CH88HB | ch8 8hb | ch88hb | Flintshire | Sir Y Fflint | Rhosesmor STW | 6344 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 319154 | 374217 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HD | CH88HD | ch8 8hd | ch88hd | Flintshire | Sir Y Fflint | Rhosesmor STW | 6415 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 319087 | 374271 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HE | CH88HE | ch8 8he | ch88he | Flintshire | Sir Y Fflint | Rhosesmor STW | 5779 | 912 | 900to1200 | 1.83 | 1.34 | 0.98 | 17 | 9.07 | 10.02 | 319468 | 373720 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HF | CH88HF | ch8 8hf | ch88hf | Flintshire | Sir Y Fflint | Rhosesmor STW | 4341 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 319839 | 372331 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HG | CH88HG | ch8 8hg | ch88hg | Flintshire | Sir Y Fflint | Rhosesmor STW | 5261 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 319667 | 373238 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HH | CH88HH | ch8 8hh | ch88hh | Flintshire | Sir Y Fflint | Rhosesmor STW | 4411 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 319638 | 372344 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HJ | CH88HJ | ch8 8hj | ch88hj | Flintshire | Sir Y Fflint | Rhosesmor STW | 4222 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320197 | 372294 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HL | CH88HL | ch8 8hl | ch88hl | Flintshire | Sir Y Fflint | Rhosesmor STW | 4196 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320201 | 372268 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HN | CH88HN | ch8 8hn | ch88hn | Flintshire | Sir Y Fflint | Rhosesmor STW | 4123 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320152 | 372184 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HP | CH88HP | ch8 8hp | ch88hp | Flintshire | Sir Y Fflint | Rhosesmor STW | 4215 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320057 | 372257 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HQ | CH88HQ | ch8 8hq | ch88hq | Flintshire | Sir Y Fflint | Rhosesmor STW | 4614 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 320003 | 372653 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HR | CH88HR | ch8 8hr | ch88hr | Flintshire | Sir Y Fflint | Rhosesmor STW | 4509 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 320011 | 372548 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HS | CH88HS | ch8 8hs | ch88hs | Flintshire | Sir Y Fflint | Rhosesmor STW | 4270 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 319865 | 372265 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HT | CH88HT | ch8 8ht | ch88ht | Flintshire | Sir Y Fflint | Rhosesmor STW | 4095 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320201 | 372165 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HU | CH88HU | ch8 8hu | ch88hu | Flintshire | Sir Y Fflint | Rhosesmor STW | 4008 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320181 | 372072 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HW | CH88HW | ch8 8hw | ch88hw | Flintshire | Sir Y Fflint | Rhosesmor STW | 4383 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320058 | 372429 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HX | CH88HX | ch8 8hx | ch88hx | Flintshire | Sir Y Fflint | Rhosesmor STW | 4001 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320321 | 372092 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8HZ | CH88HZ | ch8 8hz | ch88hz | Flintshire | Sir Y Fflint | Rhosesmor STW | 4371 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 319718 | 372327 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8JA | CH88JA | ch8 8ja | ch88ja | Flintshire | Sir Y Fflint | Rhosesmor STW | 4638 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 319659 | 372588 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8JB | CH88JB | ch8 8jb | ch88jb | Flintshire | Sir Y Fflint | Rhosesmor STW | 4507 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 319912 | 372522 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8JD | CH88JD | ch8 8jd | ch88jd | Flintshire | Sir Y Fflint | Rhosesmor STW | 4401 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320014 | 372438 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8JE | CH88JE | ch8 8je | ch88je | Flintshire | Sir Y Fflint | Rhosesmor STW | 4306 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320006 | 372338 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8JF | CH88JF | ch8 8jf | ch88jf | Flintshire | Sir Y Fflint | Rhosesmor STW | 4389 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 319919 | 372402 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8JP | CH88JP | ch8 8jp | ch88jp | Flintshire | Sir Y Fflint | Rhosesmor STW | 4928 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 319785 | 372924 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8JU | CH88JU | ch8 8ju | ch88ju | Flintshire | Sir Y Fflint | Rhosesmor STW | 4574 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 319812 | 372565 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8JX | CH88JX | ch8 8jx | ch88jx | Flintshire | Sir Y Fflint | Rhosesmor STW | 4527 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 319756 | 372501 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8JY | CH88JY | ch8 8jy | ch88jy | Flintshire | Sir Y Fflint | Rhosesmor STW | 4455 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 319811 | 372442 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8JZ | CH88JZ | ch8 8jz | ch88jz | Flintshire | Sir Y Fflint | Rhosesmor STW | 4591 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 319824 | 372586 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8LD | CH88LD | ch8 8ld | ch88ld | Flintshire | Sir Y Fflint | Rhosesmor STW | 7634 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 317589 | 374977 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8LN | CH88LN | ch8 8ln | ch88ln | Flintshire | Sir Y Fflint | Rhosesmor STW | 3877 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320348 | 371971 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8NH | CH88NH | ch8 8nh | ch88nh | Flintshire | Sir Y Fflint | Rhosesmor STW | 9401 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316796 | 376555 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8NN | CH88NN | ch8 8nn | ch88nn | Flintshire | Sir Y Fflint | Rhosesmor STW | 9286 | 890 | 700to900 | 1.78 | 1.3 | 0.96 | 16.59 | 8.85 | 9.78 | 316935 | 376496 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8NT | CH88NT | ch8 8nt | ch88nt | Flintshire | Sir Y Fflint | Rhosesmor STW | 9505 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316734 | 376641 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8NU | CH88NU | ch8 8nu | ch88nu | Flintshire | Sir Y Fflint | Rhosesmor STW | 9625 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316464 | 376636 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8NW | CH88NW | ch8 8nw | ch88nw | Flintshire | Sir Y Fflint | Rhosesmor STW | 9650 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316498 | 376682 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8NX | CH88NX | ch8 8nx | ch88nx | Flintshire | Sir Y Fflint | Rhosesmor STW | 9640 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316446 | 376643 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8NY | CH88NY | ch8 8ny | ch88ny | Flintshire | Sir Y Fflint | Rhosesmor STW | 9704 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316418 | 376701 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8NZ | CH88NZ | ch8 8nz | ch88nz | Flintshire | Sir Y Fflint | Rhosesmor STW | 9534 | 890 | 700to900 | 1.78 | 1.3 | 0.96 | 16.59 | 8.85 | 9.78 | 316373 | 376482 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8PA | CH88PA | ch8 8pa | ch88pa | Flintshire | Sir Y Fflint | Rhosesmor STW | 9442 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316720 | 376563 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8PD | CH88PD | ch8 8pd | ch88pd | Flintshire | Sir Y Fflint | Rhosesmor STW | 9466 | 890 | 700to900 | 1.78 | 1.3 | 0.96 | 16.59 | 8.85 | 9.78 | 316425 | 376434 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8QA | CH88QA | ch8 8qa | ch88qa | Flintshire | Sir Y Fflint | Rhosesmor STW | 10356 | 882 | 700to900 | 1.77 | 1.29 | 0.95 | 16.44 | 8.77 | 9.69 | 315255 | 376763 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8QN | CH88QN | ch8 8qn | ch88qn | Flintshire | Sir Y Fflint | Rhosesmor STW | 9784 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316816 | 376991 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8QP | CH88QP | ch8 8qp | ch88qp | Flintshire | Sir Y Fflint | Rhosesmor STW | 9952 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316043 | 376776 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8QR | CH88QR | ch8 8qr | ch88qr | Flintshire | Sir Y Fflint | Rhosesmor STW | 9878 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316176 | 376766 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8QT | CH88QT | ch8 8qt | ch88qt | Flintshire | Sir Y Fflint | Rhosesmor STW | 9842 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316388 | 376841 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8QW | CH88QW | ch8 8qw | ch88qw | Flintshire | Sir Y Fflint | Rhosesmor STW | 9960 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316216 | 376882 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8QY | CH88QY | ch8 8qy | ch88qy | Flintshire | Sir Y Fflint | Rhosesmor STW | 10255 | 882 | 700to900 | 1.77 | 1.29 | 0.95 | 16.44 | 8.77 | 9.69 | 315355 | 376707 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8QZ | CH88QZ | ch8 8qz | ch88qz | Flintshire | Sir Y Fflint | Rhosesmor STW | 10417 | 882 | 700to900 | 1.77 | 1.29 | 0.95 | 16.44 | 8.77 | 9.69 | 315027 | 376680 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8RH | CH88RH | ch8 8rh | ch88rh | Flintshire | Sir Y Fflint | Rhosesmor STW | 9882 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316209 | 376789 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8RJ | CH88RJ | ch8 8rj | ch88rj | Flintshire | Sir Y Fflint | Rhosesmor STW | 9895 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316215 | 376808 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8RP | CH88RP | ch8 8rp | ch88rp | Flintshire | Sir Y Fflint | Rhosesmor STW | 10088 | 882 | 700to900 | 1.77 | 1.29 | 0.95 | 16.44 | 8.77 | 9.69 | 315346 | 376501 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8RR | CH88RR | ch8 8rr | ch88rr | Flintshire | Sir Y Fflint | Rhosesmor STW | 9999 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316075 | 376848 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8SH | CH88SH | ch8 8sh | ch88sh | Flintshire | Sir Y Fflint | Rhosesmor STW | 9581 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316761 | 376739 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8SJ | CH88SJ | ch8 8sj | ch88sj | Flintshire | Sir Y Fflint | Rhosesmor STW | 9699 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316538 | 376758 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8SL | CH88SL | ch8 8sl | ch88sl | Flintshire | Sir Y Fflint | Rhosesmor STW | 9581 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316694 | 376706 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8SN | CH88SN | ch8 8sn | ch88sn | Flintshire | Sir Y Fflint | Rhosesmor STW | 12775 | 856 | 700to900 | 1.71 | 1.25 | 0.92 | 15.95 | 8.51 | 9.4 | 313645 | 378590 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8SP | CH88SP | ch8 8sp | ch88sp | Flintshire | Sir Y Fflint | Rhosesmor STW | 9662 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316606 | 376752 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8SQ | CH88SQ | ch8 8sq | ch88sq | Flintshire | Sir Y Fflint | Rhosesmor STW | 9737 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316653 | 376859 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8SR | CH88SR | ch8 8sr | ch88sr | Flintshire | Sir Y Fflint | Rhosesmor STW | 9626 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 316784 | 376800 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8ST | CH88ST | ch8 8st | ch88st | Flintshire | Sir Y Fflint | Rhosesmor STW | 9094 | 890 | 700to900 | 1.78 | 1.3 | 0.96 | 16.59 | 8.85 | 9.78 | 317213 | 376415 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8SU | CH88SU | ch8 8su | ch88su | Flintshire | Sir Y Fflint | Rhosesmor STW | 7952 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 317503 | 375289 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8SW | CH88SW | ch8 8sw | ch88sw | Flintshire | Sir Y Fflint | Rhosesmor STW | 9454 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 317968 | 377101 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 8SZ | CH88SZ | ch8 8sz | ch88sz | Flintshire | Sir Y Fflint | Rhosesmor STW | 8066 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 318140 | 375689 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AB | CH89AB | ch8 9ab | ch89ab | Flintshire | Sir Y Fflint | Rhosesmor STW | 15857 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313201 | 381951 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AE | CH89AE | ch8 9ae | ch89ae | Flintshire | Sir Y Fflint | Rhosesmor STW | 10638 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 315636 | 377333 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AF | CH89AF | ch8 9af | ch89af | Flintshire | Sir Y Fflint | Rhosesmor STW | 11569 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 314782 | 377902 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AG | CH89AG | ch8 9ag | ch89ag | Flintshire | Sir Y Fflint | Rhosesmor STW | 11995 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 314560 | 378265 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AH | CH89AH | ch8 9ah | ch89ah | Flintshire | Sir Y Fflint | Rhosesmor STW | 11866 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 314600 | 378138 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AJ | CH89AJ | ch8 9aj | ch89aj | Flintshire | Sir Y Fflint | Rhosesmor STW | 11823 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 314769 | 378193 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AL | CH89AL | ch8 9al | ch89al | Flintshire | Sir Y Fflint | Rhosesmor STW | 11863 | 874 | 700to900 | 1.75 | 1.28 | 0.94 | 16.29 | 8.69 | 9.6 | 314474 | 378052 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AN | CH89AN | ch8 9an | ch89an | Flintshire | Sir Y Fflint | Rhosesmor STW | 13100 | 856 | 700to900 | 1.71 | 1.25 | 0.92 | 15.95 | 8.51 | 9.4 | 313898 | 379153 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AP | CH89AP | ch8 9ap | ch89ap | Flintshire | Sir Y Fflint | Rhosesmor STW | 12006 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 314664 | 378343 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AR | CH89AR | ch8 9ar | ch89ar | Flintshire | Sir Y Fflint | Rhosesmor STW | 13920 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 313347 | 379772 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AS | CH89AS | ch8 9as | ch89as | Flintshire | Sir Y Fflint | Rhosesmor STW | 13468 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 314009 | 379657 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AW | CH89AW | ch8 9aw | ch89aw | Flintshire | Sir Y Fflint | Rhosesmor STW | 13488 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 314074 | 379719 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AY | CH89AY | ch8 9ay | ch89ay | Flintshire | Sir Y Fflint | Rhosesmor STW | 13596 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 314041 | 379825 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9AZ | CH89AZ | ch8 9az | ch89az | Flintshire | Sir Y Fflint | Rhosesmor STW | 13648 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 314070 | 379903 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BB | CH89BB | ch8 9bb | ch89bb | Flintshire | Sir Y Fflint | Rhosesmor STW | 14955 | 848 | 700to900 | 1.7 | 1.24 | 0.91 | 15.81 | 8.43 | 9.32 | 311841 | 379966 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BD | CH89BD | ch8 9bd | ch89bd | Flintshire | Sir Y Fflint | Rhosesmor STW | 15180 | 848 | 700to900 | 1.7 | 1.24 | 0.91 | 15.81 | 8.43 | 9.32 | 311850 | 380256 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BE | CH89BE | ch8 9be | ch89be | Flintshire | Sir Y Fflint | Rhosesmor STW | 15182 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 312625 | 380807 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BG | CH89BG | ch8 9bg | ch89bg | Flintshire | Sir Y Fflint | Rhosesmor STW | 16665 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 311118 | 381562 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BH | CH89BH | ch8 9bh | ch89bh | Flintshire | Sir Y Fflint | Rhosesmor STW | 15161 | 848 | 700to900 | 1.7 | 1.24 | 0.91 | 15.81 | 8.43 | 9.32 | 311686 | 380107 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BJ | CH89BJ | ch8 9bj | ch89bj | Flintshire | Sir Y Fflint | Rhosesmor STW | 16395 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 311690 | 381639 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BL | CH89BL | ch8 9bl | ch89bl | Flintshire | Sir Y Fflint | Rhosesmor STW | 16347 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 311761 | 381629 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BN | CH89BN | ch8 9bn | ch89bn | Flintshire | Sir Y Fflint | Rhosesmor STW | 15020 | 848 | 700to900 | 1.7 | 1.24 | 0.91 | 15.81 | 8.43 | 9.32 | 311728 | 379961 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BP | CH89BP | ch8 9bp | ch89bp | Flintshire | Sir Y Fflint | Rhosesmor STW | 15025 | 848 | 700to900 | 1.7 | 1.24 | 0.91 | 15.81 | 8.43 | 9.32 | 311746 | 379981 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BQ | CH89BQ | ch8 9bq | ch89bq | Flintshire | Sir Y Fflint | Rhosesmor STW | 16242 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 311888 | 381589 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BT | CH89BT | ch8 9bt | ch89bt | Flintshire | Sir Y Fflint | Rhosesmor STW | 15015 | 848 | 700to900 | 1.7 | 1.24 | 0.91 | 15.81 | 8.43 | 9.32 | 311778 | 379993 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BW | CH89BW | ch8 9bw | ch89bw | Flintshire | Sir Y Fflint | Rhosesmor STW | 15038 | 848 | 700to900 | 1.7 | 1.24 | 0.91 | 15.81 | 8.43 | 9.32 | 311663 | 379932 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BY | CH89BY | ch8 9by | ch89by | Flintshire | Sir Y Fflint | Rhosesmor STW | 15087 | 848 | 700to900 | 1.7 | 1.24 | 0.91 | 15.81 | 8.43 | 9.32 | 311690 | 380016 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9BZ | CH89BZ | ch8 9bz | ch89bz | Flintshire | Sir Y Fflint | Rhosesmor STW | 14827 | 848 | 700to900 | 1.7 | 1.24 | 0.91 | 15.81 | 8.43 | 9.32 | 311841 | 379804 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9DJ | CH89DJ | ch8 9dj | ch89dj | Flintshire | Sir Y Fflint | Rhosesmor STW | 15833 | 855 | 700to900 | 1.71 | 1.25 | 0.92 | 15.94 | 8.5 | 9.39 | 310804 | 380256 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9DN | CH89DN | ch8 9dn | ch89dn | Flintshire | Sir Y Fflint | Rhosesmor STW | 10133 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 318942 | 378068 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9DP | CH89DP | ch8 9dp | ch89dp | Flintshire | Sir Y Fflint | Rhosesmor STW | 10810 | 790 | 700to900 | 1.58 | 1.16 | 0.85 | 14.72 | 7.85 | 8.68 | 318368 | 378631 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9DQ | CH89DQ | ch8 9dq | ch89dq | Flintshire | Sir Y Fflint | Rhosesmor STW | 10933 | 790 | 700to900 | 1.58 | 1.16 | 0.85 | 14.72 | 7.85 | 8.68 | 318287 | 378737 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9DU | CH89DU | ch8 9du | ch89du | Flintshire | Sir Y Fflint | Rhosesmor STW | 10571 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 317634 | 378167 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9DW | CH89DW | ch8 9dw | ch89dw | Flintshire | Sir Y Fflint | Rhosesmor STW | 9753 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 319386 | 377765 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9DX | CH89DX | ch8 9dx | ch89dx | Flintshire | Sir Y Fflint | Rhosesmor STW | 11196 | 790 | 700to900 | 1.58 | 1.16 | 0.85 | 14.72 | 7.85 | 8.68 | 317926 | 378912 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9DZ | CH89DZ | ch8 9dz | ch89dz | Flintshire | Sir Y Fflint | Rhosesmor STW | 12082 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 316887 | 379506 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9EA | CH89EA | ch8 9ea | ch89ea | Flintshire | Sir Y Fflint | Rhosesmor STW | 15046 | 848 | 700to900 | 1.7 | 1.24 | 0.91 | 15.81 | 8.43 | 9.32 | 311792 | 380044 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9ED | CH89ED | ch8 9ed | ch89ed | Flintshire | Sir Y Fflint | Rhosesmor STW | 11742 | 806 | 700to900 | 1.61 | 1.18 | 0.87 | 15.02 | 8.01 | 8.86 | 316876 | 379140 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9EF | CH89EF | ch8 9ef | ch89ef | Flintshire | Sir Y Fflint | Rhosesmor STW | 11987 | 806 | 700to900 | 1.61 | 1.18 | 0.87 | 15.02 | 8.01 | 8.86 | 317072 | 379471 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9EG | CH89EG | ch8 9eg | ch89eg | Flintshire | Sir Y Fflint | Rhosesmor STW | 11805 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 316321 | 378984 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9EJ | CH89EJ | ch8 9ej | ch89ej | Flintshire | Sir Y Fflint | Rhosesmor STW | 11941 | 806 | 700to900 | 1.61 | 1.18 | 0.87 | 15.02 | 8.01 | 8.86 | 316797 | 379323 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9EN | CH89EN | ch8 9en | ch89en | Flintshire | Sir Y Fflint | Rhosesmor STW | 11072 | 857 | 700to900 | 1.72 | 1.26 | 0.92 | 15.97 | 8.52 | 9.42 | 315384 | 377688 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9EP | CH89EP | ch8 9ep | ch89ep | Flintshire | Sir Y Fflint | Rhosesmor STW | 11426 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 316419 | 378613 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9EQ | CH89EQ | ch8 9eq | ch89eq | Flintshire | Sir Y Fflint | Rhosesmor STW | 11711 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 315747 | 378613 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9ER | CH89ER | ch8 9er | ch89er | Flintshire | Sir Y Fflint | Rhosesmor STW | 10582 | 873 | 700to900 | 1.75 | 1.28 | 0.94 | 16.27 | 8.68 | 9.59 | 315908 | 377422 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9ES | CH89ES | ch8 9es | ch89es | Flintshire | Sir Y Fflint | Rhosesmor STW | 10716 | 837 | 700to900 | 1.68 | 1.23 | 0.9 | 15.6 | 8.32 | 9.2 | 316834 | 378019 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9EZ | CH89EZ | ch8 9ez | ch89ez | Flintshire | Sir Y Fflint | Rhosesmor STW | 14150 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 315216 | 381059 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9FP | CH89FP | ch8 9fp | ch89fp | Flintshire | Sir Y Fflint | Rhosesmor STW | 12502 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316358 | 379754 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9GA | CH89GA | ch8 9ga | ch89ga | Flintshire | Sir Y Fflint | Rhosesmor STW | 12532 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 316546 | 379860 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HA | CH89HA | ch8 9ha | ch89ha | Flintshire | Sir Y Fflint | Rhosesmor STW | 15308 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 314168 | 381844 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HB | CH89HB | ch8 9hb | ch89hb | Flintshire | Sir Y Fflint | Rhosesmor STW | 15316 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313921 | 381727 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HD | CH89HD | ch8 9hd | ch89hd | Flintshire | Sir Y Fflint | Rhosesmor STW | 13959 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 315424 | 380942 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HE | CH89HE | ch8 9he | ch89he | Flintshire | Sir Y Fflint | Rhosesmor STW | 13937 | 772 | 700to900 | 1.55 | 1.13 | 0.83 | 14.39 | 7.67 | 8.48 | 315567 | 380980 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HF | CH89HF | ch8 9hf | ch89hf | Flintshire | Sir Y Fflint | Rhosesmor STW | 13027 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316197 | 380255 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HG | CH89HG | ch8 9hg | ch89hg | Flintshire | Sir Y Fflint | Rhosesmor STW | 15770 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313314 | 381915 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HH | CH89HH | ch8 9hh | ch89hh | Flintshire | Sir Y Fflint | Rhosesmor STW | 15672 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313449 | 381877 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HJ | CH89HJ | ch8 9hj | ch89hj | Flintshire | Sir Y Fflint | Rhosesmor STW | 15846 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 312993 | 381819 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HL | CH89HL | ch8 9hl | ch89hl | Flintshire | Sir Y Fflint | Rhosesmor STW | 15857 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313260 | 381984 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HN | CH89HN | ch8 9hn | ch89hn | Flintshire | Sir Y Fflint | Rhosesmor STW | 14288 | 809 | 700to900 | 1.62 | 1.18 | 0.87 | 15.08 | 8.04 | 8.89 | 314497 | 380867 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HP | CH89HP | ch8 9hp | ch89hp | Flintshire | Sir Y Fflint | Rhosesmor STW | 16105 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 312950 | 382093 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HQ | CH89HQ | ch8 9hq | ch89hq | Flintshire | Sir Y Fflint | Rhosesmor STW | 15716 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313296 | 381842 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HR | CH89HR | ch8 9hr | ch89hr | Flintshire | Sir Y Fflint | Rhosesmor STW | 16055 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313019 | 382075 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HS | CH89HS | ch8 9hs | ch89hs | Flintshire | Sir Y Fflint | Rhosesmor STW | 16174 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 312857 | 382119 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HT | CH89HT | ch8 9ht | ch89ht | Flintshire | Sir Y Fflint | Rhosesmor STW | 16198 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 312826 | 382128 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HU | CH89HU | ch8 9hu | ch89hu | Flintshire | Sir Y Fflint | Rhosesmor STW | 16399 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 312885 | 382394 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HW | CH89HW | ch8 9hw | ch89hw | Flintshire | Sir Y Fflint | Rhosesmor STW | 13251 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315921 | 380384 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HX | CH89HX | ch8 9hx | ch89hx | Flintshire | Sir Y Fflint | Rhosesmor STW | 13277 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315997 | 380444 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HY | CH89HY | ch8 9hy | ch89hy | Flintshire | Sir Y Fflint | Rhosesmor STW | 15863 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313111 | 381906 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9HZ | CH89HZ | ch8 9hz | ch89hz | Flintshire | Sir Y Fflint | Rhosesmor STW | 15839 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313019 | 381826 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JA | CH89JA | ch8 9ja | ch89ja | Flintshire | Sir Y Fflint | Rhosesmor STW | 15676 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313231 | 381760 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JB | CH89JB | ch8 9jb | ch89jb | Flintshire | Sir Y Fflint | Rhosesmor STW | 17394 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 311793 | 382901 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JD | CH89JD | ch8 9jd | ch89jd | Flintshire | Sir Y Fflint | Rhosesmor STW | 12493 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 316573 | 379828 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JE | CH89JE | ch8 9je | ch89je | Flintshire | Sir Y Fflint | Rhosesmor STW | 15849 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 312973 | 381810 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JF | CH89JF | ch8 9jf | ch89jf | Flintshire | Sir Y Fflint | Rhosesmor STW | 15950 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 312776 | 381810 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JG | CH89JG | ch8 9jg | ch89jg | Flintshire | Sir Y Fflint | Rhosesmor STW | 16561 | 808 | 700to900 | 1.62 | 1.18 | 0.87 | 15.06 | 8.03 | 8.88 | 312300 | 382236 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JH | CH89JH | ch8 9jh | ch89jh | Flintshire | Sir Y Fflint | Rhosesmor STW | 17638 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 311693 | 383126 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JJ | CH89JJ | ch8 9jj | ch89jj | Flintshire | Sir Y Fflint | Rhosesmor STW | 15893 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313209 | 381997 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JL | CH89JL | ch8 9jl | ch89jl | Flintshire | Sir Y Fflint | Rhosesmor STW | 15726 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313090 | 381736 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JN | CH89JN | ch8 9jn | ch89jn | Flintshire | Sir Y Fflint | Rhosesmor STW | 18682 | 734 | 700to900 | 1.47 | 1.07 | 0.79 | 13.68 | 7.29 | 8.06 | 310781 | 383782 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JP | CH89JP | ch8 9jp | ch89jp | Flintshire | Sir Y Fflint | Rhosesmor STW | 17119 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 312027 | 382723 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JQ | CH89JQ | ch8 9jq | ch89jq | Flintshire | Sir Y Fflint | Rhosesmor STW | 16154 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 312881 | 382110 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JR | CH89JR | ch8 9jr | ch89jr | Flintshire | Sir Y Fflint | Rhosesmor STW | 15796 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313077 | 381809 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JS | CH89JS | ch8 9js | ch89js | Flintshire | Sir Y Fflint | Rhosesmor STW | 18304 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 310982 | 383462 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JT | CH89JT | ch8 9jt | ch89jt | Flintshire | Sir Y Fflint | Rhosesmor STW | 17839 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311182 | 383038 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JU | CH89JU | ch8 9ju | ch89ju | Flintshire | Sir Y Fflint | Rhosesmor STW | 18022 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311039 | 383162 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JW | CH89JW | ch8 9jw | ch89jw | Flintshire | Sir Y Fflint | Rhosesmor STW | 19216 | 726 | 700to900 | 1.45 | 1.06 | 0.78 | 13.53 | 7.21 | 7.97 | 310498 | 384235 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JX | CH89JX | ch8 9jx | ch89jx | Flintshire | Sir Y Fflint | Rhosesmor STW | 17965 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311049 | 383100 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9JY | CH89JY | ch8 9jy | ch89jy | Flintshire | Sir Y Fflint | Rhosesmor STW | 17515 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 311766 | 383027 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LA | CH89LA | ch8 9la | ch89la | Flintshire | Sir Y Fflint | Rhosesmor STW | 15726 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313147 | 381769 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LD | CH89LD | ch8 9ld | ch89ld | Flintshire | Sir Y Fflint | Rhosesmor STW | 17918 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311112 | 383086 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LE | CH89LE | ch8 9le | ch89le | Flintshire | Sir Y Fflint | Rhosesmor STW | 17913 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311161 | 383112 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LF | CH89LF | ch8 9lf | ch89lf | Flintshire | Sir Y Fflint | Rhosesmor STW | 17934 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311253 | 383197 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LH | CH89LH | ch8 9lh | ch89lh | Flintshire | Sir Y Fflint | Rhosesmor STW | 17938 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311037 | 383060 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LJ | CH89LJ | ch8 9lj | ch89lj | Flintshire | Sir Y Fflint | Rhosesmor STW | 17955 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311015 | 383066 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LL | CH89LL | ch8 9ll | ch89ll | Flintshire | Sir Y Fflint | Rhosesmor STW | 17891 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311058 | 383017 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LN | CH89LN | ch8 9ln | ch89ln | Flintshire | Sir Y Fflint | Rhosesmor STW | 17836 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311094 | 382975 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LS | CH89LS | ch8 9ls | ch89ls | Flintshire | Sir Y Fflint | Rhosesmor STW | 17702 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311155 | 382855 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LT | CH89LT | ch8 9lt | ch89lt | Flintshire | Sir Y Fflint | Rhosesmor STW | 17532 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311116 | 382624 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LU | CH89LU | ch8 9lu | ch89lu | Flintshire | Sir Y Fflint | Rhosesmor STW | 17540 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 310778 | 382397 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LW | CH89LW | ch8 9lw | ch89lw | Flintshire | Sir Y Fflint | Rhosesmor STW | 17800 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 311076 | 382920 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LY | CH89LY | ch8 9ly | ch89ly | Flintshire | Sir Y Fflint | Rhosesmor STW | 16932 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 310668 | 381558 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9LZ | CH89LZ | ch8 9lz | ch89lz | Flintshire | Sir Y Fflint | Rhosesmor STW | 16832 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 310945 | 381642 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9NA | CH89NA | ch8 9na | ch89na | Flintshire | Sir Y Fflint | Rhosesmor STW | 17921 | 820 | 700to900 | 1.64 | 1.2 | 0.88 | 15.28 | 8.15 | 9.01 | 308938 | 381396 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9NB | CH89NB | ch8 9nb | ch89nb | Flintshire | Sir Y Fflint | Rhosesmor STW | 16884 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 310636 | 381472 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9ND | CH89ND | ch8 9nd | ch89nd | Flintshire | Sir Y Fflint | Rhosesmor STW | 16885 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 310654 | 381487 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9NE | CH89NE | ch8 9ne | ch89ne | Flintshire | Sir Y Fflint | Rhosesmor STW | 17028 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 310360 | 381438 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9NF | CH89NF | ch8 9nf | ch89nf | Flintshire | Sir Y Fflint | Rhosesmor STW | 16773 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 310671 | 381359 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9NH | CH89NH | ch8 9nh | ch89nh | Flintshire | Sir Y Fflint | Rhosesmor STW | 18853 | 734 | 700to900 | 1.47 | 1.07 | 0.79 | 13.68 | 7.29 | 8.06 | 310638 | 383893 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9NJ | CH89NJ | ch8 9nj | ch89nj | Flintshire | Sir Y Fflint | Rhosesmor STW | 16750 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 310680 | 381337 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9NS | CH89NS | ch8 9ns | ch89ns | Flintshire | Sir Y Fflint | Rhosesmor STW | 12833 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315945 | 379941 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9NU | CH89NU | ch8 9nu | ch89nu | Flintshire | Sir Y Fflint | Rhosesmor STW | 12694 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315986 | 379807 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9NX | CH89NX | ch8 9nx | ch89nx | Flintshire | Sir Y Fflint | Rhosesmor STW | 12488 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316265 | 379701 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9NY | CH89NY | ch8 9ny | ch89ny | Flintshire | Sir Y Fflint | Rhosesmor STW | 12318 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316464 | 379598 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9NZ | CH89NZ | ch8 9nz | ch89nz | Flintshire | Sir Y Fflint | Rhosesmor STW | 12082 | 806 | 700to900 | 1.61 | 1.18 | 0.87 | 15.02 | 8.01 | 8.86 | 316731 | 379449 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9PD | CH89PD | ch8 9pd | ch89pd | Flintshire | Sir Y Fflint | Rhosesmor STW | 12404 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316404 | 379667 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9PE | CH89PE | ch8 9pe | ch89pe | Flintshire | Sir Y Fflint | Rhosesmor STW | 12664 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316183 | 379858 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9PF | CH89PF | ch8 9pf | ch89pf | Flintshire | Sir Y Fflint | Rhosesmor STW | 12607 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316335 | 379858 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9PG | CH89PG | ch8 9pg | ch89pg | Flintshire | Sir Y Fflint | Rhosesmor STW | 12465 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316452 | 379751 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9PJ | CH89PJ | ch8 9pj | ch89pj | Flintshire | Sir Y Fflint | Rhosesmor STW | 12538 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316305 | 379771 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9PN | CH89PN | ch8 9pn | ch89pn | Flintshire | Sir Y Fflint | Rhosesmor STW | 12705 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316253 | 379931 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9PQ | CH89PQ | ch8 9pq | ch89pq | Flintshire | Sir Y Fflint | Rhosesmor STW | 12323 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 316548 | 379636 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9PR | CH89PR | ch8 9pr | ch89pr | Flintshire | Sir Y Fflint | Rhosesmor STW | 12736 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316089 | 379897 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9PS | CH89PS | ch8 9ps | ch89ps | Flintshire | Sir Y Fflint | Rhosesmor STW | 12726 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316063 | 379875 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9PT | CH89PT | ch8 9pt | ch89pt | Flintshire | Sir Y Fflint | Rhosesmor STW | 12608 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 316165 | 379790 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9PY | CH89PY | ch8 9py | ch89py | Flintshire | Sir Y Fflint | Rhosesmor STW | 12809 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315990 | 379934 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9PZ | CH89PZ | ch8 9pz | ch89pz | Flintshire | Sir Y Fflint | Rhosesmor STW | 12743 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315970 | 379854 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QA | CH89QA | ch8 9qa | ch89qa | Flintshire | Sir Y Fflint | Rhosesmor STW | 13323 | 816 | 700to900 | 1.63 | 1.2 | 0.88 | 15.21 | 8.11 | 8.97 | 315498 | 380279 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QB | CH89QB | ch8 9qb | ch89qb | Flintshire | Sir Y Fflint | Rhosesmor STW | 12690 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315673 | 379663 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QE | CH89QE | ch8 9qe | ch89qe | Flintshire | Sir Y Fflint | Rhosesmor STW | 13373 | 816 | 700to900 | 1.63 | 1.2 | 0.88 | 15.21 | 8.11 | 8.97 | 315438 | 380307 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QF | CH89QF | ch8 9qf | ch89qf | Flintshire | Sir Y Fflint | Rhosesmor STW | 13263 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315730 | 380316 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QH | CH89QH | ch8 9qh | ch89qh | Flintshire | Sir Y Fflint | Rhosesmor STW | 13320 | 816 | 700to900 | 1.63 | 1.2 | 0.88 | 15.21 | 8.11 | 8.97 | 315080 | 380077 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QL | CH89QL | ch8 9ql | ch89ql | Flintshire | Sir Y Fflint | Rhosesmor STW | 13420 | 816 | 700to900 | 1.63 | 1.2 | 0.88 | 15.21 | 8.11 | 8.97 | 315449 | 380364 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QR | CH89QR | ch8 9qr | ch89qr | Flintshire | Sir Y Fflint | Rhosesmor STW | 13241 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315706 | 380282 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QS | CH89QS | ch8 9qs | ch89qs | Flintshire | Sir Y Fflint | Rhosesmor STW | 11929 | 806 | 700to900 | 1.61 | 1.18 | 0.87 | 15.02 | 8.01 | 8.86 | 316916 | 379354 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QU | CH89QU | ch8 9qu | ch89qu | Flintshire | Sir Y Fflint | Rhosesmor STW | 13099 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315853 | 380191 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QW | CH89QW | ch8 9qw | ch89qw | Flintshire | Sir Y Fflint | Rhosesmor STW | 13342 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315613 | 380352 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QX | CH89QX | ch8 9qx | ch89qx | Flintshire | Sir Y Fflint | Rhosesmor STW | 13328 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315657 | 380356 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QY | CH89QY | ch8 9qy | ch89qy | Flintshire | Sir Y Fflint | Rhosesmor STW | 13228 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315735 | 380281 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9QZ | CH89QZ | ch8 9qz | ch89qz | Flintshire | Sir Y Fflint | Rhosesmor STW | 13218 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 315563 | 380193 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9RB | CH89RB | ch8 9rb | ch89rb | Flintshire | Sir Y Fflint | Rhosesmor STW | 18499 | 734 | 700to900 | 1.47 | 1.07 | 0.79 | 13.68 | 7.29 | 8.06 | 312271 | 384454 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9RD | CH89RD | ch8 9rd | ch89rd | Flintshire | Sir Y Fflint | Rhosesmor STW | 18523 | 734 | 700to900 | 1.47 | 1.07 | 0.79 | 13.68 | 7.29 | 8.06 | 312190 | 384437 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9RE | CH89RE | ch8 9re | ch89re | Flintshire | Sir Y Fflint | Rhosesmor STW | 18499 | 734 | 700to900 | 1.47 | 1.07 | 0.79 | 13.68 | 7.29 | 8.06 | 312228 | 384430 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9RF | CH89RF | ch8 9rf | ch89rf | Flintshire | Sir Y Fflint | Rhosesmor STW | 18534 | 734 | 700to900 | 1.47 | 1.07 | 0.79 | 13.68 | 7.29 | 8.06 | 312262 | 384488 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9RG | CH89RG | ch8 9rg | ch89rg | Flintshire | Sir Y Fflint | Rhosesmor STW | 18538 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 312277 | 384501 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9RH | CH89RH | ch8 9rh | ch89rh | Flintshire | Sir Y Fflint | Rhosesmor STW | 18582 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 312345 | 384587 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9RL | CH89RL | ch8 9rl | ch89rl | Flintshire | Sir Y Fflint | Rhosesmor STW | 18219 | 734 | 700to900 | 1.47 | 1.07 | 0.79 | 13.68 | 7.29 | 8.06 | 311847 | 383896 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9RP | CH89RP | ch8 9rp | ch89rp | Flintshire | Sir Y Fflint | Rhosesmor STW | 18738 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 312333 | 384756 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9RQ | CH89RQ | ch8 9rq | ch89rq | Flintshire | Sir Y Fflint | Rhosesmor STW | 18569 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 312311 | 384554 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9RR | CH89RR | ch8 9rr | ch89rr | Flintshire | Sir Y Fflint | Rhosesmor STW | 18703 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 312263 | 384680 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9RS | CH89RS | ch8 9rs | ch89rs | Flintshire | Sir Y Fflint | Rhosesmor STW | 18856 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 312095 | 384764 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9RT | CH89RT | ch8 9rt | ch89rt | Flintshire | Sir Y Fflint | Rhosesmor STW | 18701 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 312163 | 384625 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SA | CH89SA | ch8 9sa | ch89sa | Flintshire | Sir Y Fflint | Rhosesmor STW | 18774 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 312165 | 384708 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SB | CH89SB | ch8 9sb | ch89sb | Flintshire | Sir Y Fflint | Rhosesmor STW | 18751 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 312248 | 384727 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SD | CH89SD | ch8 9sd | ch89sd | Flintshire | Sir Y Fflint | Rhosesmor STW | 15437 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 314095 | 381951 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SH | CH89SH | ch8 9sh | ch89sh | Flintshire | Sir Y Fflint | Rhosesmor STW | 15540 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 314019 | 382028 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SJ | CH89SJ | ch8 9sj | ch89sj | Flintshire | Sir Y Fflint | Rhosesmor STW | 15595 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313957 | 382059 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SL | CH89SL | ch8 9sl | ch89sl | Flintshire | Sir Y Fflint | Rhosesmor STW | 15657 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313891 | 382094 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SN | CH89SN | ch8 9sn | ch89sn | Flintshire | Sir Y Fflint | Rhosesmor STW | 15887 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313639 | 382223 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SP | CH89SP | ch8 9sp | ch89sp | Flintshire | Sir Y Fflint | Rhosesmor STW | 15680 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313867 | 382108 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SR | CH89SR | ch8 9sr | ch89sr | Flintshire | Sir Y Fflint | Rhosesmor STW | 15930 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313591 | 382246 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9ST | CH89ST | ch8 9st | ch89st | Flintshire | Sir Y Fflint | Rhosesmor STW | 15973 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313530 | 382263 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SU | CH89SU | ch8 9su | ch89su | Flintshire | Sir Y Fflint | Rhosesmor STW | 16012 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313480 | 382280 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SW | CH89SW | ch8 9sw | ch89sw | Flintshire | Sir Y Fflint | Rhosesmor STW | 15938 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313606 | 382263 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SX | CH89SX | ch8 9sx | ch89sx | Flintshire | Sir Y Fflint | Rhosesmor STW | 15761 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313809 | 382169 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SY | CH89SY | ch8 9sy | ch89sy | Flintshire | Sir Y Fflint | Rhosesmor STW | 15508 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313879 | 381921 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9SZ | CH89SZ | ch8 9sz | ch89sz | Flintshire | Sir Y Fflint | Rhosesmor STW | 16151 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313323 | 382354 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9TD | CH89TD | ch8 9td | ch89td | Flintshire | Sir Y Fflint | Rhosesmor STW | 15981 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313434 | 382221 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9TE | CH89TE | ch8 9te | ch89te | Flintshire | Sir Y Fflint | Rhosesmor STW | 16070 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313403 | 382305 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9TF | CH89TF | ch8 9tf | ch89tf | Flintshire | Sir Y Fflint | Rhosesmor STW | 16101 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313357 | 382316 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9TG | CH89TG | ch8 9tg | ch89tg | Flintshire | Sir Y Fflint | Rhosesmor STW | 16135 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313275 | 382310 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9TN | CH89TN | ch8 9tn | ch89tn | Flintshire | Sir Y Fflint | Rhosesmor STW | 15633 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313945 | 382095 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9TQ | CH89TQ | ch8 9tq | ch89tq | Flintshire | Sir Y Fflint | Rhosesmor STW | 16121 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313320 | 382318 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9TR | CH89TR | ch8 9tr | ch89tr | Flintshire | Sir Y Fflint | Rhosesmor STW | 15839 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313721 | 382212 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9TS | CH89TS | ch8 9ts | ch89ts | Flintshire | Sir Y Fflint | Rhosesmor STW | 15863 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313731 | 382244 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9TT | CH89TT | ch8 9tt | ch89tt | Flintshire | Sir Y Fflint | Rhosesmor STW | 15900 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313655 | 382246 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9TW | CH89TW | ch8 9tw | ch89tw | Flintshire | Sir Y Fflint | Rhosesmor STW | 15687 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313886 | 382126 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9UB | CH89UB | ch8 9ub | ch89ub | Flintshire | Sir Y Fflint | Rhosesmor STW | 15937 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313677 | 382299 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9UD | CH89UD | ch8 9ud | ch89ud | Flintshire | Sir Y Fflint | Rhosesmor STW | 15923 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313622 | 382255 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9UE | CH89UE | ch8 9ue | ch89ue | Flintshire | Sir Y Fflint | Rhosesmor STW | 15969 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313569 | 382279 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9UF | CH89UF | ch8 9uf | ch89uf | Flintshire | Sir Y Fflint | Rhosesmor STW | 16028 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313485 | 382301 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9UG | CH89UG | ch8 9ug | ch89ug | Flintshire | Sir Y Fflint | Rhosesmor STW | 16080 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313418 | 382324 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9UJ | CH89UJ | ch8 9uj | ch89uj | Flintshire | Sir Y Fflint | Rhosesmor STW | 16030 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313585 | 382356 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9UL | CH89UL | ch8 9ul | ch89ul | Flintshire | Sir Y Fflint | Rhosesmor STW | 16066 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313565 | 382386 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9UN | CH89UN | ch8 9un | ch89un | Flintshire | Sir Y Fflint | Rhosesmor STW | 16033 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313602 | 382369 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9UP | CH89UP | ch8 9up | ch89up | Flintshire | Sir Y Fflint | Rhosesmor STW | 16086 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313575 | 382414 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9UR | CH89UR | ch8 9ur | ch89ur | Flintshire | Sir Y Fflint | Rhosesmor STW | 16119 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313402 | 382360 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9US | CH89US | ch8 9us | ch89us | Flintshire | Sir Y Fflint | Rhosesmor STW | 16257 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 313211 | 382414 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9UT | CH89UT | ch8 9ut | ch89ut | Flintshire | Sir Y Fflint | Rhosesmor STW | 15964 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 313504 | 382239 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9UU | CH89UU | ch8 9uu | ch89uu | Flintshire | Sir Y Fflint | Rhosesmor STW | 16804 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 312643 | 382722 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
CH8 9ZW | CH89ZW | ch8 9zw | ch89zw | Flintshire | Sir Y Fflint | Rhosesmor STW | 5459 | 771 | 700to900 | 1.54 | 1.13 | 0.83 | 14.37 | 7.66 | 8.47 | 323909 | 372767 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL18 6BU | LL186BU | ll18 6bu | ll186bu | Flintshire | Sir Y Fflint | Rhosesmor STW | 17472 | 820 | 700to900 | 1.64 | 1.2 | 0.88 | 15.28 | 8.15 | 9.01 | 308657 | 380509 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL18 6DY | LL186DY | ll18 6dy | ll186dy | Flintshire | Sir Y Fflint | Rhosesmor STW | 16740 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 309624 | 380423 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL18 6EJ | LL186EJ | ll18 6ej | ll186ej | Flintshire | Sir Y Fflint | Rhosesmor STW | 18750 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 307452 | 381103 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL18 6EL | LL186EL | ll18 6el | ll186el | Flintshire | Sir Y Fflint | Rhosesmor STW | 18775 | 806 | 700to900 | 1.61 | 1.18 | 0.87 | 15.02 | 8.01 | 8.86 | 307599 | 381292 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL18 6EP | LL186EP | ll18 6ep | ll186ep | Flintshire | Sir Y Fflint | Rhosesmor STW | 18865 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 307479 | 381298 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL18 6EQ | LL186EQ | ll18 6eq | ll186eq | Flintshire | Sir Y Fflint | Rhosesmor STW | 18705 | 806 | 700to900 | 1.61 | 1.18 | 0.87 | 15.02 | 8.01 | 8.86 | 307775 | 381369 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL18 6ER | LL186ER | ll18 6er | ll186er | Flintshire | Sir Y Fflint | Rhosesmor STW | 18611 | 806 | 700to900 | 1.61 | 1.18 | 0.87 | 15.02 | 8.01 | 8.86 | 307592 | 381049 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL18 6EW | LL186EW | ll18 6ew | ll186ew | Flintshire | Sir Y Fflint | Rhosesmor STW | 18648 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 307466 | 380970 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL18 6LG | LL186LG | ll18 6lg | ll186lg | Flintshire | Sir Y Fflint | Rhosesmor STW | 18722 | 806 | 700to900 | 1.61 | 1.18 | 0.87 | 15.02 | 8.01 | 8.86 | 307557 | 381173 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9SQ | LL199SQ | ll19 9sq | ll199sq | Flintshire | Sir Y Fflint | Rhosesmor STW | 18790 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309556 | 383046 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9SS | LL199SS | ll19 9ss | ll199ss | Flintshire | Sir Y Fflint | Rhosesmor STW | 19630 | 719 | 700to900 | 1.44 | 1.05 | 0.77 | 13.39 | 7.14 | 7.9 | 309082 | 383740 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9SU | LL199SU | ll19 9su | ll199su | Flintshire | Sir Y Fflint | Rhosesmor STW | 19539 | 719 | 700to900 | 1.44 | 1.05 | 0.77 | 13.39 | 7.14 | 7.9 | 309206 | 383721 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9SY | LL199SY | ll19 9sy | ll199sy | Flintshire | Sir Y Fflint | Rhosesmor STW | 19318 | 719 | 700to900 | 1.44 | 1.05 | 0.77 | 13.39 | 7.14 | 7.9 | 309304 | 383518 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TA | LL199TA | ll19 9ta | ll199ta | Flintshire | Sir Y Fflint | Rhosesmor STW | 19209 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 309441 | 383485 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TB | LL199TB | ll19 9tb | ll199tb | Flintshire | Sir Y Fflint | Rhosesmor STW | 18830 | 726 | 700to900 | 1.45 | 1.06 | 0.78 | 13.53 | 7.21 | 7.97 | 310120 | 383511 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TD | LL199TD | ll19 9td | ll199td | Flintshire | Sir Y Fflint | Rhosesmor STW | 18419 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 310336 | 383161 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TE | LL199TE | ll19 9te | ll199te | Flintshire | Sir Y Fflint | Rhosesmor STW | 18679 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309872 | 383145 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TF | LL199TF | ll19 9tf | ll199tf | Flintshire | Sir Y Fflint | Rhosesmor STW | 18891 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 309405 | 383056 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TG | LL199TG | ll19 9tg | ll199tg | Flintshire | Sir Y Fflint | Rhosesmor STW | 18861 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 309482 | 383078 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TH | LL199TH | ll19 9th | ll199th | Flintshire | Sir Y Fflint | Rhosesmor STW | 18570 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309858 | 382999 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TL | LL199TL | ll19 9tl | ll199tl | Flintshire | Sir Y Fflint | Rhosesmor STW | 18640 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309740 | 382997 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TP | LL199TP | ll19 9tp | ll199tp | Flintshire | Sir Y Fflint | Rhosesmor STW | 18783 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309527 | 383015 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TQ | LL199TQ | ll19 9tq | ll199tq | Flintshire | Sir Y Fflint | Rhosesmor STW | 19052 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 309335 | 383206 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TR | LL199TR | ll19 9tr | ll199tr | Flintshire | Sir Y Fflint | Rhosesmor STW | 18746 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309556 | 382990 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TS | LL199TS | ll19 9ts | ll199ts | Flintshire | Sir Y Fflint | Rhosesmor STW | 18622 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309721 | 382960 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TT | LL199TT | ll19 9tt | ll199tt | Flintshire | Sir Y Fflint | Rhosesmor STW | 19594 | 726 | 700to900 | 1.45 | 1.06 | 0.78 | 13.53 | 7.21 | 7.97 | 310179 | 384478 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TU | LL199TU | ll19 9tu | ll199tu | Flintshire | Sir Y Fflint | Rhosesmor STW | 18590 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309771 | 382958 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TW | LL199TW | ll19 9tw | ll199tw | Flintshire | Sir Y Fflint | Rhosesmor STW | 18826 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309616 | 383137 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TX | LL199TX | ll19 9tx | ll199tx | Flintshire | Sir Y Fflint | Rhosesmor STW | 18880 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 309454 | 383080 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9TY | LL199TY | ll19 9ty | ll199ty | Flintshire | Sir Y Fflint | Rhosesmor STW | 18867 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309568 | 383152 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9UA | LL199UA | ll19 9ua | ll199ua | Flintshire | Sir Y Fflint | Rhosesmor STW | 19005 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 309475 | 383254 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9UE | LL199UE | ll19 9ue | ll199ue | Flintshire | Sir Y Fflint | Rhosesmor STW | 18918 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309532 | 383188 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9UF | LL199UF | ll19 9uf | ll199uf | Flintshire | Sir Y Fflint | Rhosesmor STW | 18794 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309688 | 383151 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9UG | LL199UG | ll19 9ug | ll199ug | Flintshire | Sir Y Fflint | Rhosesmor STW | 19000 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 309402 | 383192 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9UH | LL199UH | ll19 9uh | ll199uh | Flintshire | Sir Y Fflint | Rhosesmor STW | 18942 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 309430 | 383140 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9UL | LL199UL | ll19 9ul | ll199ul | Flintshire | Sir Y Fflint | Rhosesmor STW | 18892 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 309494 | 383126 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9UN | LL199UN | ll19 9un | ll199un | Flintshire | Sir Y Fflint | Rhosesmor STW | 18697 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309589 | 382954 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL19 9YP | LL199YP | ll19 9yp | ll199yp | Flintshire | Sir Y Fflint | Rhosesmor STW | 18774 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 309811 | 383218 | Flintshire LPA | NE |  | Cyngor Sir y Fflint | Flintshire County Council
LL54 5RA | LL545RA | ll54 5ra | ll545ra | Gwynedd | Gwynedd | Llanfaglan WwTW | 1526 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 245531 | 360433 | Gwynedd LPA | NW |  | Cyngor Gwynedd | Gwynedd Council
LL54 5RD | LL545RD | ll54 5rd | ll545rd | Gwynedd | Gwynedd | Llanfaglan WwTW | 651 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 246926 | 359948 | Gwynedd LPA | NW |  | Cyngor Gwynedd | Gwynedd Council
LL54 5RE | LL545RE | ll54 5re | ll545re | Gwynedd | Gwynedd | Llanfaglan WwTW | 568 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 246586 | 359937 | Gwynedd LPA | NW |  | Cyngor Gwynedd | Gwynedd Council
LL54 5RF | LL545RF | ll54 5rf | ll545rf | Gwynedd | Gwynedd | Llanfaglan WwTW | 1362 | 944 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.59 | 9.38 | 10.37 | 246375 | 360709 | Gwynedd LPA | NW |  | Cyngor Gwynedd | Gwynedd Council
LL54 5RG | LL545RG | ll54 5rg | ll545rg | Gwynedd | Gwynedd | Llanfaglan WwTW | 1543 | 1095 | 900to1200 | 2.19 | 1.6 | 1.18 | 20.41 | 10.88 | 12.03 | 247579 | 360583 | Gwynedd LPA | NW |  | Cyngor Gwynedd | Gwynedd Council
LL54 5RH | LL545RH | ll54 5rh | ll545rh | Gwynedd | Gwynedd | Llanfaglan WwTW | 1327 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 247176 | 360578 | Gwynedd LPA | NW |  | Cyngor Gwynedd | Gwynedd Council
LL54 5RL | LL545RL | ll54 5rl | ll545rl | Gwynedd | Gwynedd | Llanfaglan WwTW | 2050 | 1095 | 900to1200 | 2.19 | 1.6 | 1.18 | 20.41 | 10.88 | 12.03 | 247831 | 361028 | Gwynedd LPA | NW |  | Cyngor Gwynedd | Gwynedd Council
LL54 5TA | LL545TA | ll54 5ta | ll545ta | Gwynedd | Gwynedd | Llanfaglan WwTW | 3678 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 244872 | 356138 | Gwynedd LPA | NW |  | Cyngor Gwynedd | Gwynedd Council
LL54 5TF | LL545TF | ll54 5tf | ll545tf | Gwynedd | Gwynedd | Llanfaglan WwTW | 2687 | 1138 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.21 | 11.31 | 12.5 | 245530 | 356917 | Gwynedd LPA | NW |  | Cyngor Gwynedd | Gwynedd Council
LL54 5TP | LL545TP | ll54 5tp | ll545tp | Gwynedd | Gwynedd | Llanfaglan WwTW | 3054 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 243696 | 358510 | Gwynedd LPA | NW |  | Cyngor Gwynedd | Gwynedd Council
LL54 5TU | LL545TU | ll54 5tu | ll545tu | Gwynedd | Gwynedd | Llanfaglan WwTW | 885 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 247178 | 360062 | Gwynedd LPA | NW |  | Cyngor Gwynedd | Gwynedd Council
LL54 5TW | LL545TW | ll54 5tw | ll545tw | Gwynedd | Gwynedd | Llanfaglan WwTW | 3849 | 956 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.82 | 9.5 | 10.5 | 243638 | 356945 | Gwynedd LPA | NW |  | Cyngor Gwynedd | Gwynedd Council
SA16 0AJ | SA160AJ | sa16 0aj | sa160aj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20397 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242899 | 201457 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0AQ | SA160AQ | sa16 0aq | sa160aq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20606 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242830 | 201257 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0AX | SA160AX | sa16 0ax | sa160ax | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20313 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 242904 | 201542 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0AZ | SA160AZ | sa16 0az | sa160az | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20151 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 242971 | 201695 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0BQ | SA160BQ | sa16 0bq | sa160bq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 19651 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 243003 | 202196 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0BX | SA160BX | sa16 0bx | sa160bx | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 18920 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 243626 | 202839 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0DJ | SA160DJ | sa16 0dj | sa160dj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20263 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 243004 | 201576 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0DZ | SA160DZ | sa16 0dz | sa160dz | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20675 | 1134 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.14 | 11.27 | 12.46 | 242036 | 201337 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0EG | SA160EG | sa16 0eg | sa160eg | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20678 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243207 | 201124 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0EH | SA160EH | sa16 0eh | sa160eh | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20570 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243183 | 201237 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0EJ | SA160EJ | sa16 0ej | sa160ej | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 21518 | 1113 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.74 | 11.06 | 12.23 | 240883 | 200742 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0ES | SA160ES | sa16 0es | sa160es | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20703 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243181 | 201102 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0EX | SA160EX | sa16 0ex | sa160ex | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 19777 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 241652 | 202344 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0EZ | SA160EZ | sa16 0ez | sa160ez | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 19042 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 241810 | 203062 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0HA | SA160HA | sa16 0ha | sa160ha | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20666 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243273 | 201126 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0HJ | SA160HJ | sa16 0hj | sa160hj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 19447 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 241303 | 202773 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0HS | SA160HS | sa16 0hs | sa160hs | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20986 | 1168 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.77 | 11.61 | 12.83 | 243533 | 200767 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0HT | SA160HT | sa16 0ht | sa160ht | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 21239 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243279 | 200546 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0HU | SA160HU | sa16 0hu | sa160hu | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 21148 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243116 | 200662 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0HX | SA160HX | sa16 0hx | sa160hx | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20138 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 241414 | 202031 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0HY | SA160HY | sa16 0hy | sa160hy | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20847 | 1168 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.77 | 11.61 | 12.83 | 243667 | 200890 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0HZ | SA160HZ | sa16 0hz | sa160hz | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 18593 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 240892 | 203777 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0JP | SA160JP | sa16 0jp | sa160jp | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 18324 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 243519 | 203457 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0JS | SA160JS | sa16 0js | sa160js | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 19310 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 242632 | 202610 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0JT | SA160JT | sa16 0jt | sa160jt | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 18600 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 243422 | 203193 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0JU | SA160JU | sa16 0ju | sa160ju | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 19379 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 242467 | 202572 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0JX | SA160JX | sa16 0jx | sa160jx | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 19441 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 242374 | 202527 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0JY | SA160JY | sa16 0jy | sa160jy | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20650 | 1134 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.14 | 11.27 | 12.46 | 242388 | 201292 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0JZ | SA160JZ | sa16 0jz | sa160jz | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 19859 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 241666 | 202256 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0LE | SA160LE | sa16 0le | sa160le | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20725 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243277 | 201066 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0LF | SA160LF | sa16 0lf | sa160lf | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20696 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243049 | 201130 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0LJ | SA160LJ | sa16 0lj | sa160lj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20524 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242987 | 201314 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0LQ | SA160LQ | sa16 0lq | sa160lq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20538 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242934 | 201309 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0TH | SA160TH | sa16 0th | sa160th | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20875 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243457 | 200889 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0TL | SA160TL | sa16 0tl | sa160tl | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20898 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243295 | 200888 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0TN | SA160TN | sa16 0tn | sa160tn | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20912 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243098 | 200904 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0TP | SA160TP | sa16 0tp | sa160tp | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20829 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242954 | 201010 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0TR | SA160TR | sa16 0tr | sa160tr | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20758 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242905 | 201090 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0TS | SA160TS | sa16 0ts | sa160ts | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20755 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242818 | 201108 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0TT | SA160TT | sa16 0tt | sa160tt | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20863 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242775 | 201006 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0TU | SA160TU | sa16 0tu | sa160tu | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20772 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242654 | 201119 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0TW | SA160TW | sa16 0tw | sa160tw | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20835 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243170 | 200971 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0TX | SA160TX | sa16 0tx | sa160tx | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20896 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242840 | 200961 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0TY | SA160TY | sa16 0ty | sa160ty | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20683 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242736 | 201195 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UA | SA160UA | sa16 0ua | sa160ua | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20708 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242791 | 201160 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UB | SA160UB | sa16 0ub | sa160ub | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20647 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242757 | 201228 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UD | SA160UD | sa16 0ud | sa160ud | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20535 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242721 | 201348 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UE | SA160UE | sa16 0ue | sa160ue | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20550 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242684 | 201339 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UF | SA160UF | sa16 0uf | sa160uf | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20571 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242575 | 201338 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UG | SA160UG | sa16 0ug | sa160ug | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20647 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 242588 | 201258 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UH | SA160UH | sa16 0uh | sa160uh | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20402 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 242436 | 201535 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UJ | SA160UJ | sa16 0uj | sa160uj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20421 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 242325 | 201538 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UL | SA160UL | sa16 0ul | sa160ul | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20510 | 1134 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.14 | 11.27 | 12.46 | 242376 | 201437 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UN | SA160UN | sa16 0un | sa160un | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20407 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 242049 | 201609 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UP | SA160UP | sa16 0up | sa160up | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20544 | 1134 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.14 | 11.27 | 12.46 | 242230 | 201431 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UR | SA160UR | sa16 0ur | sa160ur | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20473 | 1134 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.14 | 11.27 | 12.46 | 242247 | 201500 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0US | SA160US | sa16 0us | sa160us | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20421 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 242231 | 201557 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UT | SA160UT | sa16 0ut | sa160ut | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20469 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 242121 | 201530 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UU | SA160UU | sa16 0uu | sa160uu | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20305 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 242084 | 201705 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UW | SA160UW | sa16 0uw | sa160uw | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20554 | 1134 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.14 | 11.27 | 12.46 | 242298 | 201408 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0UY | SA160UY | sa16 0uy | sa160uy | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20257 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 242126 | 201746 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0YA | SA160YA | sa16 0ya | sa160ya | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20226 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 241927 | 201820 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0YB | SA160YB | sa16 0yb | sa160yb | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20107 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 241889 | 201950 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0YD | SA160YD | sa16 0yd | sa160yd | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20504 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243043 | 201325 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0YE | SA160YE | sa16 0ye | sa160ye | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20204 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 241853 | 201859 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0YU | SA160YU | sa16 0yu | sa160yu | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20526 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243131 | 201289 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA16 0YY | SA160YY | sa16 0yy | sa160yy | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 20417 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 243066 | 201410 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4AJ | SA174AJ | sa17 4aj | sa174aj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15880 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 241084 | 206566 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4AZ | SA174AZ | sa17 4az | sa174az | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15909 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 241239 | 206482 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4LF | SA174LF | sa17 4lf | sa174lf | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15903 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 241450 | 206420 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4PP | SA174PP | sa17 4pp | sa174pp | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15703 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 241389 | 206650 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4SJ | SA174SJ | sa17 4sj | sa174sj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15861 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240741 | 206709 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4SR | SA174SR | sa17 4sr | sa174sr | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15268 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 241646 | 207024 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4ST | SA174ST | sa17 4st | sa174st | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15338 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 241553 | 206980 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4SU | SA174SU | sa17 4su | sa174su | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15905 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240834 | 206628 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4SX | SA174SX | sa17 4sx | sa174sx | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15355 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 241627 | 206939 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4SY | SA174SY | sa17 4sy | sa174sy | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16032 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240794 | 206507 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4TA | SA174TA | sa17 4ta | sa174ta | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16158 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 240840 | 206357 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4TD | SA174TD | sa17 4td | sa174td | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16094 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 240954 | 206384 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4TE | SA174TE | sa17 4te | sa174te | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15963 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 241013 | 206503 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4TF | SA174TF | sa17 4tf | sa174tf | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16444 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 240790 | 206071 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4TH | SA174TH | sa17 4th | sa174th | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16105 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 241307 | 206254 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4TN | SA174TN | sa17 4tn | sa174tn | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15868 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240984 | 206613 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4TP | SA174TP | sa17 4tp | sa174tp | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15749 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 241029 | 206724 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4TQ | SA174TQ | sa17 4tq | sa174tq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16071 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 241043 | 206378 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4TR | SA174TR | sa17 4tr | sa174tr | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15669 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 241108 | 206781 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4TS | SA174TS | sa17 4ts | sa174ts | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15630 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 241066 | 206837 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4TT | SA174TT | sa17 4tt | sa174tt | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15511 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 241113 | 206947 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4TW | SA174TW | sa17 4tw | sa174tw | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15853 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 241223 | 206547 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UD | SA174UD | sa17 4ud | sa174ud | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15755 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240932 | 206752 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UE | SA174UE | sa17 4ue | sa174ue | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16186 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 240712 | 206373 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UF | SA174UF | sa17 4uf | sa174uf | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16326 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 240701 | 206228 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UG | SA174UG | sa17 4ug | sa174ug | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16253 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 240685 | 206312 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UH | SA174UH | sa17 4uh | sa174uh | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15909 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240665 | 206687 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UL | SA174UL | sa17 4ul | sa174ul | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16002 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 240425 | 206679 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UN | SA174UN | sa17 4un | sa174un | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16212 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 240264 | 206517 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UP | SA174UP | sa17 4up | sa174up | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16187 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 240472 | 206463 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UQ | SA174UQ | sa17 4uq | sa174uq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16321 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 240357 | 206363 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UR | SA174UR | sa17 4ur | sa174ur | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16208 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 240331 | 206495 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4US | SA174US | sa17 4us | sa174us | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16053 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240559 | 206573 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UT | SA174UT | sa17 4ut | sa174ut | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16011 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240500 | 206640 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UU | SA174UU | sa17 4uu | sa174uu | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15781 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240720 | 206803 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UW | SA174UW | sa17 4uw | sa174uw | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16339 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 240155 | 206424 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UX | SA174UX | sa17 4ux | sa174ux | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16291 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 240301 | 206418 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4UZ | SA174UZ | sa17 4uz | sa174uz | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15862 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240574 | 206772 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 4YB | SA174YB | sa17 4yb | sa174yb | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15822 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240695 | 206768 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5AJ | SA175AJ | sa17 5aj | sa175aj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15677 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240734 | 206908 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5AX | SA175AX | sa17 5ax | sa175ax | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15610 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240789 | 206959 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5AY | SA175AY | sa17 5ay | sa175ay | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14118 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239985 | 208935 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5AZ | SA175AZ | sa17 5az | sa175az | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15570 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240788 | 207002 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5BD | SA175BD | sa17 5bd | sa175bd | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15488 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240649 | 207143 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5BJ | SA175BJ | sa17 5bj | sa175bj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15438 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240728 | 207167 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5BQ | SA175BQ | sa17 5bq | sa175bq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15532 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240853 | 207019 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5BX | SA175BX | sa17 5bx | sa175bx | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15374 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240830 | 207196 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5DQ | SA175DQ | sa17 5dq | sa175dq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15579 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240724 | 207017 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5EF | SA175EF | sa17 5ef | sa175ef | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15570 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 240348 | 207176 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5EG | SA175EG | sa17 5eg | sa175eg | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15275 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240540 | 207416 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5EH | SA175EH | sa17 5eh | sa175eh | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15491 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 240384 | 207247 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5EJ | SA175EJ | sa17 5ej | sa175ej | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15581 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 240135 | 207254 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5EQ | SA175EQ | sa17 5eq | sa175eq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15440 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240537 | 207239 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5EX | SA175EX | sa17 5ex | sa175ex | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16247 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 238826 | 207135 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5EZ | SA175EZ | sa17 5ez | sa175ez | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16215 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 238235 | 207493 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5HJ | SA175HJ | sa17 5hj | sa175hj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16846 | 1115 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.78 | 11.08 | 12.25 | 237151 | 207414 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5HQ | SA175HQ | sa17 5hq | sa175hq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 17031 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 237511 | 206972 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5HX | SA175HX | sa17 5hx | sa175hx | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 16223 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 237602 | 207865 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5HZ | SA175HZ | sa17 5hz | sa175hz | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15833 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 238008 | 208072 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JA | SA175JA | sa17 5ja | sa175ja | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15696 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 238429 | 207980 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JB | SA175JB | sa17 5jb | sa175jb | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15503 | 1263 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.54 | 12.55 | 13.88 | 239246 | 207756 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JD | SA175JD | sa17 5jd | sa175jd | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15539 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 238453 | 208148 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JE | SA175JE | sa17 5je | sa175je | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15621 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 238489 | 208032 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JF | SA175JF | sa17 5jf | sa175jf | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15573 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 238465 | 208102 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JG | SA175JG | sa17 5jg | sa175jg | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15571 | 1263 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.54 | 12.55 | 13.88 | 238502 | 208082 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JH | SA175JH | sa17 5jh | sa175jh | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15530 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 238492 | 208136 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JJ | SA175JJ | sa17 5jj | sa175jj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15476 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 238461 | 208216 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JL | SA175JL | sa17 5jl | sa175jl | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15420 | 1263 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.54 | 12.55 | 13.88 | 238580 | 208212 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JN | SA175JN | sa17 5jn | sa175jn | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15459 | 1263 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.54 | 12.55 | 13.88 | 238520 | 208201 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JP | SA175JP | sa17 5jp | sa175jp | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15320 | 1263 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.54 | 12.55 | 13.88 | 239382 | 207893 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JQ | SA175JQ | sa17 5jq | sa175jq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15512 | 1263 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.54 | 12.55 | 13.88 | 238530 | 208135 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JR | SA175JR | sa17 5jr | sa175jr | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14682 | 1303 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.29 | 12.95 | 14.32 | 240261 | 208180 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JS | SA175JS | sa17 5js | sa175js | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15929 | 1263 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.54 | 12.55 | 13.88 | 238756 | 207532 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JT | SA175JT | sa17 5jt | sa175jt | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15304 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240731 | 207309 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JU | SA175JU | sa17 5ju | sa175ju | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15610 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 238419 | 208086 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JW | SA175JW | sa17 5jw | sa175jw | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14764 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 238788 | 208850 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5JX | SA175JX | sa17 5jx | sa175jx | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15665 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 238411 | 208027 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5RN | SA175RN | sa17 5rn | sa175rn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14338 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236642 | 210331 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5RP | SA175RP | sa17 5rp | sa175rp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14380 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236627 | 210292 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5RR | SA175RR | sa17 5rr | sa175rr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14440 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236690 | 210203 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5RS | SA175RS | sa17 5rs | sa175rs | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14257 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236831 | 210346 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5RT | SA175RT | sa17 5rt | sa175rt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14203 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236728 | 210442 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5RU | SA175RU | sa17 5ru | sa175ru | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14200 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236754 | 210436 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5RW | SA175RW | sa17 5rw | sa175rw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14354 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236613 | 210325 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5RX | SA175RX | sa17 5rx | sa175rx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14426 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236670 | 210226 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5RY | SA175RY | sa17 5ry | sa175ry | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14142 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236773 | 210490 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SA | SA175SA | sa17 5sa | sa175sa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14144 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236803 | 210477 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SB | SA175SB | sa17 5sb | sa175sb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14126 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236803 | 210496 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SD | SA175SD | sa17 5sd | sa175sd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14100 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 236844 | 210508 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SE | SA175SE | sa17 5se | sa175se | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14159 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 236659 | 210516 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SF | SA175SF | sa17 5sf | sa175sf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14333 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236558 | 210369 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SG | SA175SG | sa17 5sg | sa175sg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14372 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236589 | 210315 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SH | SA175SH | sa17 5sh | sa175sh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14496 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236560 | 210193 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SL | SA175SL | sa17 5sl | sa175sl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14632 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236503 | 210069 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SN | SA175SN | sa17 5sn | sa175sn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14703 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 236484 | 210001 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SP | SA175SP | sa17 5sp | sa175sp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14799 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236545 | 209874 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SR | SA175SR | sa17 5sr | sa175sr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 15017 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236503 | 209657 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SS | SA175SS | sa17 5ss | sa175ss | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 15096 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 236472 | 209584 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5ST | SA175ST | sa17 5st | sa175st | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14875 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 236482 | 209817 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SU | SA175SU | sa17 5su | sa175su | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14305 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236708 | 210341 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SW | SA175SW | sa17 5sw | sa175sw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14690 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236516 | 210002 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5SY | SA175SY | sa17 5sy | sa175sy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 15182 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 236389 | 209524 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TA | SA175TA | sa17 5ta | sa175ta | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14063 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 236820 | 210557 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TB | SA175TB | sa17 5tb | sa175tb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14225 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236684 | 210436 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TD | SA175TD | sa17 5td | sa175td | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14189 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236706 | 210466 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TE | SA175TE | sa17 5te | sa175te | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13808 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 236975 | 210771 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TF | SA175TF | sa17 5tf | sa175tf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13674 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 237045 | 210888 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TG | SA175TG | sa17 5tg | sa175tg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13779 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 237166 | 210732 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TH | SA175TH | sa17 5th | sa175th | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13580 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 237213 | 210927 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TJ | SA175TJ | sa17 5tj | sa175tj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13867 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 237128 | 210652 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TL | SA175TL | sa17 5tl | sa175tl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13326 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 237386 | 211135 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TN | SA175TN | sa17 5tn | sa175tn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13370 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 237214 | 211150 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TP | SA175TP | sa17 5tp | sa175tp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 11408 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 238893 | 212675 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TQ | SA175TQ | sa17 5tq | sa175tq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13638 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 237248 | 210852 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TR | SA175TR | sa17 5tr | sa175tr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 11996 | 1333 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.85 | 13.25 | 14.65 | 238460 | 212185 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TS | SA175TS | sa17 5ts | sa175ts | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13877 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 237090 | 210655 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TT | SA175TT | sa17 5tt | sa175tt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13526 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 237135 | 211013 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TU | SA175TU | sa17 5tu | sa175tu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 15390 | 1143 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.3 | 11.36 | 12.56 | 236349 | 209317 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TW | SA175TW | sa17 5tw | sa175tw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 11862 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 237858 | 212520 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5TY | SA175TY | sa17 5ty | sa175ty | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 15147 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 236541 | 209504 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UA | SA175UA | sa17 5ua | sa175ua | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 15588 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 236609 | 209010 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UB | SA175UB | sa17 5ub | sa175ub | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 15153 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 237165 | 209281 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UD | SA175UD | sa17 5ud | sa175ud | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14722 | 1292 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.08 | 12.84 | 14.2 | 237673 | 209575 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UE | SA175UE | sa17 5ue | sa175ue | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14611 | 1292 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.08 | 12.84 | 14.2 | 237952 | 209567 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UF | SA175UF | sa17 5uf | sa175uf | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15161 | 1273 | 1200to1500 | 2.55 | 1.86 | 1.37 | 23.73 | 12.65 | 13.99 | 238105 | 208803 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UG | SA175UG | sa17 5ug | sa175ug | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 15854 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 237290 | 208508 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UH | SA175UH | sa17 5uh | sa175uh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 16549 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 236559 | 208011 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UL | SA175UL | sa17 5ul | sa175ul | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 16591 | 1138 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.21 | 11.31 | 12.5 | 236278 | 208063 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UN | SA175UN | sa17 5un | sa175un | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 15972 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 236500 | 208641 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UR | SA175UR | sa17 5ur | sa175ur | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13967 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 237013 | 210588 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5US | SA175US | sa17 5us | sa175us | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13876 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 237534 | 210504 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UT | SA175UT | sa17 5ut | sa175ut | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14116 | 1292 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.08 | 12.84 | 14.2 | 237504 | 210261 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UU | SA175UU | sa17 5uu | sa175uu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13220 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 237680 | 211146 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5UY | SA175UY | sa17 5uy | sa175uy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13168 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 238228 | 211033 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YB | SA175YB | sa17 5yb | sa175yb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 12932 | 1354 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.24 | 13.46 | 14.88 | 238570 | 211184 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YD | SA175YD | sa17 5yd | sa175yd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13370 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 238277 | 210809 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YE | SA175YE | sa17 5ye | sa175ye | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 13107 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 239367 | 210436 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YF | SA175YF | sa17 5yf | sa175yf | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14184 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 238969 | 209417 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YG | SA175YG | sa17 5yg | sa175yg | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14313 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 238535 | 209535 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YH | SA175YH | sa17 5yh | sa175yh | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14501 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 239163 | 208937 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YJ | SA175YJ | sa17 5yj | sa175yj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14744 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 238708 | 208920 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YL | SA175YL | sa17 5yl | sa175yl | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14752 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 238749 | 208887 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YN | SA175YN | sa17 5yn | sa175yn | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14778 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 238997 | 208713 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YP | SA175YP | sa17 5yp | sa175yp | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14864 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 238773 | 208743 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YQ | SA175YQ | sa17 5yq | sa175yq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15868 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240677 | 206726 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YR | SA175YR | sa17 5yr | sa175yr | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14607 | 1273 | 1200to1500 | 2.55 | 1.86 | 1.37 | 23.73 | 12.65 | 13.99 | 238488 | 209216 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YW | SA175YW | sa17 5yw | sa175yw | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 14737 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 239326 | 208578 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA17 5YY | SA175YY | sa17 5yy | sa175yy | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 15868 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 240677 | 206726 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QU | SA313QU | sa31 3qu | sa313qu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 6118 | 1354 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.24 | 13.46 | 14.88 | 239714 | 217957 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DB | SA328DB | sa32 8db | sa328db | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 6638 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 242390 | 216192 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DD | SA328DD | sa32 8dd | sa328dd | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 7011 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 242327 | 215780 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DE | SA328DE | sa32 8de | sa328de | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 7786 | 1459 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.19 | 14.5 | 16.03 | 242093 | 215006 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DG | SA328DG | sa32 8dg | sa328dg | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 7299 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 242077 | 215603 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DH | SA328DH | sa32 8dh | sa328dh | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 7318 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 241701 | 215862 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DJ | SA328DJ | sa32 8dj | sa328dj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 6563 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 242273 | 216373 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DQ | SA328DQ | sa32 8dq | sa328dq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 7111 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 242272 | 215697 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DS | SA328DS | sa32 8ds | sa328ds | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 7384 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 240764 | 216393 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DT | SA328DT | sa32 8dt | sa328dt | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 7542 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 241221 | 215978 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DU | SA328DU | sa32 8du | sa328du | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 8322 | 1413 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.34 | 14.05 | 15.52 | 241099 | 215058 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DX | SA328DX | sa32 8dx | sa328dx | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 9134 | 1442 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.88 | 14.33 | 15.84 | 241250 | 213947 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DY | SA328DY | sa32 8dy | sa328dy | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 9462 | 1442 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.88 | 14.33 | 15.84 | 240625 | 213985 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8DZ | SA328DZ | sa32 8dz | sa328dz | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 10477 | 1392 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.94 | 13.84 | 15.29 | 240400 | 212900 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8ED | SA328ED | sa32 8ed | sa328ed | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 6450 | 1436 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.76 | 14.27 | 15.78 | 243097 | 215961 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5AA | SA335AA | sa33 5aa | sa335aa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 7291 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 238761 | 217082 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5AB | SA335AB | sa33 5ab | sa335ab | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 7613 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 238708 | 216753 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5AD | SA335AD | sa33 5ad | sa335ad | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 8106 | 1364 | 1200to1500 | 2.73 | 2 | 1.46 | 25.42 | 13.56 | 14.99 | 238549 | 216284 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5AE | SA335AE | sa33 5ae | sa335ae | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 8672 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 238278 | 215785 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5AF | SA335AF | sa33 5af | sa335af | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 8646 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 238352 | 215781 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5AG | SA335AG | sa33 5ag | sa335ag | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 8826 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 238267 | 215622 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5AL | SA335AL | sa33 5al | sa335al | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 12415 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 235547 | 212988 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5AN | SA335AN | sa33 5an | sa335an | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 12665 | 1372 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.57 | 13.64 | 15.07 | 234506 | 213361 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5AQ | SA335AQ | sa33 5aq | sa335aq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 8440 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 238277 | 216040 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5AX | SA335AX | sa33 5ax | sa335ax | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 8752 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 238480 | 215611 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5BB | SA335BB | sa33 5bb | sa335bb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 8690 | 1364 | 1200to1500 | 2.73 | 2 | 1.46 | 25.42 | 13.56 | 14.99 | 238909 | 215513 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5BD | SA335BD | sa33 5bd | sa335bd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 7903 | 1364 | 1200to1500 | 2.73 | 2 | 1.46 | 25.42 | 13.56 | 14.99 | 239257 | 216225 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5BE | SA335BE | sa33 5be | sa335be | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 8467 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 238461 | 215929 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5BG | SA335BG | sa33 5bg | sa335bg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 7457 | 1356 | 1200to1500 | 2.71 | 1.99 | 1.46 | 25.27 | 13.48 | 14.9 | 239601 | 216581 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5BH | SA335BH | sa33 5bh | sa335bh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 6809 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 238409 | 217808 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5DW | SA335DW | sa33 5dw | sa335dw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 8137 | 1364 | 1200to1500 | 2.73 | 2 | 1.46 | 25.42 | 13.56 | 14.99 | 238648 | 216208 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5EX | SA335EX | sa33 5ex | sa335ex | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13321 | 1290 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.04 | 12.82 | 14.17 | 236215 | 211617 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5EY | SA335EY | sa33 5ey | sa335ey | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14297 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235314 | 210970 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5EZ | SA335EZ | sa33 5ez | sa335ez | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14229 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235390 | 211008 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5HA | SA335HA | sa33 5ha | sa335ha | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14040 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235063 | 211394 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5HB | SA335HB | sa33 5hb | sa335hb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13602 | 1317 | 1200to1500 | 2.64 | 1.93 | 1.41 | 24.55 | 13.09 | 14.47 | 234764 | 212072 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5HD | SA335HD | sa33 5hd | sa335hd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13624 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 234031 | 212523 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5HF | SA335HF | sa33 5hf | sa335hf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13598 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 233859 | 212677 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5HQ | SA335HQ | sa33 5hq | sa335hq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 13787 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 233725 | 212541 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JD | SA335JD | sa33 5jd | sa335jd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14514 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235192 | 210789 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JG | SA335JG | sa33 5jg | sa335jg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14617 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235011 | 210767 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JH | SA335JH | sa33 5jh | sa335jh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14687 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 234953 | 210719 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JJ | SA335JJ | sa33 5jj | sa335jj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14776 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 234770 | 210716 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JN | SA335JN | sa33 5jn | sa335jn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14784 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 234819 | 210680 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JP | SA335JP | sa33 5jp | sa335jp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14797 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 234900 | 210622 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JQ | SA335JQ | sa33 5jq | sa335jq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14553 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235089 | 210799 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JR | SA335JR | sa33 5jr | sa335jr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14609 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235048 | 210757 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JS | SA335JS | sa33 5js | sa335js | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14625 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235103 | 210710 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JT | SA335JT | sa33 5jt | sa335jt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14692 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235056 | 210659 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JU | SA335JU | sa33 5ju | sa335ju | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14707 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235013 | 210664 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JW | SA335JW | sa33 5jw | sa335jw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14440 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235165 | 210886 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JX | SA335JX | sa33 5jx | sa335jx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 15304 | 1139 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.23 | 11.32 | 12.51 | 234737 | 210135 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JY | SA335JY | sa33 5jy | sa335jy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14436 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235147 | 210900 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5JZ | SA335JZ | sa33 5jz | sa335jz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14414 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235180 | 210908 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LA | SA335LA | sa33 5la | sa335la | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14354 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235138 | 210997 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LB | SA335LB | sa33 5lb | sa335lb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14333 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235128 | 211026 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LE | SA335LE | sa33 5le | sa335le | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14301 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235162 | 211045 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LF | SA335LF | sa33 5lf | sa335lf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14269 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235159 | 211082 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LG | SA335LG | sa33 5lg | sa335lg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14220 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235025 | 211210 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LH | SA335LH | sa33 5lh | sa335lh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14345 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235215 | 210967 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LJ | SA335LJ | sa33 5lj | sa335lj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14315 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235226 | 210995 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LL | SA335LL | sa33 5ll | sa335ll | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14374 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235296 | 210893 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LN | SA335LN | sa33 5ln | sa335ln | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14528 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235246 | 210746 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LP | SA335LP | sa33 5lp | sa335lp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14595 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235127 | 210731 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LT | SA335LT | sa33 5lt | sa335lt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 15743 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 233620 | 210263 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LW | SA335LW | sa33 5lw | sa335lw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14580 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 235371 | 210625 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5LX | SA335LX | sa33 5lx | sa335lx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 14327 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 234660 | 211292 | Carmarthenshire LPA | CA |  | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA43 1PP | SA431PP | sa43 1pp | sa431pp | Ceredigion | Sir Ceredigion | Verwig STW | 1952 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 216328 | 249416 | Ceredigion LPA | CE |  | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PR | SA431PR | sa43 1pr | sa431pr | Ceredigion | Sir Ceredigion | Verwig STW | 1948 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 216402 | 249938 | Ceredigion LPA | CE |  | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3LP | SA433LP | sa43 3lp | sa433lp | Pembrokeshire | Sir Benfro | Cardigan WwTW | 3980 | 893 | 700to900 | 1.79 | 1.31 | 0.96 | 16.64 | 8.88 | 9.81 | 214207 | 248956 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA61 1AD | SA611AD | sa61 1ad | sa611ad | Pembrokeshire | Sir Benfro | Keeston WwTW | 5867 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194649 | 214236 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BF | SA611BF | sa61 1bf | sa611bf | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DH | SA611DH | sa61 1dh | sa611dh | Pembrokeshire | Sir Benfro | Keeston WwTW | 4119 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 193250 | 215355 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DJ | SA611DJ | sa61 1dj | sa611dj | Pembrokeshire | Sir Benfro | Keeston WwTW | 4000 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 193049 | 215359 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DL | SA611DL | sa61 1dl | sa611dl | Pembrokeshire | Sir Benfro | Keeston WwTW | 4158 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 193381 | 215405 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DN | SA611DN | sa61 1dn | sa611dn | Pembrokeshire | Sir Benfro | Keeston WwTW | 4278 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 193486 | 215336 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DQ | SA611DQ | sa61 1dq | sa611dq | Pembrokeshire | Sir Benfro | Keeston WwTW | 3907 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 192936 | 215396 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DR | SA611DR | sa61 1dr | sa611dr | Pembrokeshire | Sir Benfro | Keeston WwTW | 4340 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193626 | 215371 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DS | SA611DS | sa61 1ds | sa611ds | Pembrokeshire | Sir Benfro | Keeston WwTW | 4273 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193534 | 215381 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DT | SA611DT | sa61 1dt | sa611dt | Pembrokeshire | Sir Benfro | Keeston WwTW | 4414 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193703 | 215339 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DU | SA611DU | sa61 1du | sa611du | Pembrokeshire | Sir Benfro | Keeston WwTW | 4461 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193814 | 215375 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DW | SA611DW | sa61 1dw | sa611dw | Pembrokeshire | Sir Benfro | Keeston WwTW | 4434 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193695 | 215306 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DX | SA611DX | sa61 1dx | sa611dx | Pembrokeshire | Sir Benfro | Keeston WwTW | 4617 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194030 | 215364 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DY | SA611DY | sa61 1dy | sa611dy | Pembrokeshire | Sir Benfro | Keeston WwTW | 4779 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194158 | 215262 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DZ | SA611DZ | sa61 1dz | sa611dz | Pembrokeshire | Sir Benfro | Keeston WwTW | 4775 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194232 | 215342 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EB | SA611EB | sa61 1eb | sa611eb | Pembrokeshire | Sir Benfro | Keeston WwTW | 5361 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 194107 | 214446 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1ED | SA611ED | sa61 1ed | sa611ed | Pembrokeshire | Sir Benfro | Keeston WwTW | 5237 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194304 | 214771 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EE | SA611EE | sa61 1ee | sa611ee | Pembrokeshire | Sir Benfro | Keeston WwTW | 5483 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 194290 | 214436 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EF | SA611EF | sa61 1ef | sa611ef | Pembrokeshire | Sir Benfro | Keeston WwTW | 5325 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194177 | 214548 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EH | SA611EH | sa61 1eh | sa611eh | Pembrokeshire | Sir Benfro | Keeston WwTW | 5267 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194635 | 215051 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EJ | SA611EJ | sa61 1ej | sa611ej | Pembrokeshire | Sir Benfro | Keeston WwTW | 5304 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194632 | 214994 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EL | SA611EL | sa61 1el | sa611el | Pembrokeshire | Sir Benfro | Keeston WwTW | 5416 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194642 | 214844 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EN | SA611EN | sa61 1en | sa611en | Pembrokeshire | Sir Benfro | Keeston WwTW | 5366 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194293 | 214591 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EP | SA611EP | sa61 1ep | sa611ep | Pembrokeshire | Sir Benfro | Keeston WwTW | 5286 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194494 | 214882 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1ES | SA611ES | sa61 1es | sa611es | Pembrokeshire | Sir Benfro | Keeston WwTW | 5098 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194082 | 214763 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1ET | SA611ET | sa61 1et | sa611et | Pembrokeshire | Sir Benfro | Keeston WwTW | 4977 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194210 | 215038 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EU | SA611EU | sa61 1eu | sa611eu | Pembrokeshire | Sir Benfro | Keeston WwTW | 4999 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194059 | 214874 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EW | SA611EW | sa61 1ew | sa611ew | Pembrokeshire | Sir Benfro | Keeston WwTW | 5253 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194231 | 214686 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EX | SA611EX | sa61 1ex | sa611ex | Pembrokeshire | Sir Benfro | Keeston WwTW | 4997 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194024 | 214847 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EY | SA611EY | sa61 1ey | sa611ey | Pembrokeshire | Sir Benfro | Keeston WwTW | 4918 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193739 | 214723 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EZ | SA611EZ | sa61 1ez | sa611ez | Pembrokeshire | Sir Benfro | Keeston WwTW | 5040 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194017 | 214785 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1FA | SA611FA | sa61 1fa | sa611fa | Pembrokeshire | Sir Benfro | Keeston WwTW | 5129 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193920 | 214595 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1FB | SA611FB | sa61 1fb | sa611fb | Pembrokeshire | Sir Benfro | Keeston WwTW | 5181 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194001 | 214591 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1FD | SA611FD | sa61 1fd | sa611fd | Pembrokeshire | Sir Benfro | Keeston WwTW | 5190 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193950 | 214541 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1FE | SA611FE | sa61 1fe | sa611fe | Pembrokeshire | Sir Benfro | Keeston WwTW | 5218 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194112 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HA | SA611HA | sa61 1ha | sa611ha | Pembrokeshire | Sir Benfro | Keeston WwTW | 4901 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193953 | 214912 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HG | SA611HG | sa61 1hg | sa611hg | Pembrokeshire | Sir Benfro | Keeston WwTW | 5035 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194162 | 214916 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HH | SA611HH | sa61 1hh | sa611hh | Pembrokeshire | Sir Benfro | Keeston WwTW | 5020 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194123 | 214901 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HJ | SA611HJ | sa61 1hj | sa611hj | Pembrokeshire | Sir Benfro | Keeston WwTW | 4848 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194075 | 215089 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HL | SA611HL | sa61 1hl | sa611hl | Pembrokeshire | Sir Benfro | Keeston WwTW | 4908 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194174 | 215098 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HN | SA611HN | sa61 1hn | sa611hn | Pembrokeshire | Sir Benfro | Keeston WwTW | 5847 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194718 | 214323 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HQ | SA611HQ | sa61 1hq | sa611hq | Pembrokeshire | Sir Benfro | Keeston WwTW | 4814 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193961 | 215034 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HS | SA611HS | sa61 1hs | sa611hs | Pembrokeshire | Sir Benfro | Keeston WwTW | 4801 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194022 | 215105 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HT | SA611HT | sa61 1ht | sa611ht | Pembrokeshire | Sir Benfro | Keeston WwTW | 4693 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193861 | 215107 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HU | SA611HU | sa61 1hu | sa611hu | Pembrokeshire | Sir Benfro | Keeston WwTW | 4734 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193986 | 215162 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HX | SA611HX | sa61 1hx | sa611hx | Pembrokeshire | Sir Benfro | Keeston WwTW | 4794 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194120 | 215204 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HY | SA611HY | sa61 1hy | sa611hy | Pembrokeshire | Sir Benfro | Keeston WwTW | 4683 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193965 | 215212 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HZ | SA611HZ | sa61 1hz | sa611hz | Pembrokeshire | Sir Benfro | Keeston WwTW | 4591 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193935 | 215309 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JA | SA611JA | sa61 1ja | sa611ja | Pembrokeshire | Sir Benfro | Keeston WwTW | 4891 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194305 | 215251 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JB | SA611JB | sa61 1jb | sa611jb | Pembrokeshire | Sir Benfro | Keeston WwTW | 4914 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194255 | 215168 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JD | SA611JD | sa61 1jd | sa611jd | Pembrokeshire | Sir Benfro | Keeston WwTW | 4818 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194200 | 215249 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JE | SA611JE | sa61 1je | sa611je | Pembrokeshire | Sir Benfro | Keeston WwTW | 4826 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194190 | 215228 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JF | SA611JF | sa61 1jf | sa611jf | Pembrokeshire | Sir Benfro | Keeston WwTW | 5024 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194264 | 215024 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JG | SA611JG | sa61 1jg | sa611jg | Pembrokeshire | Sir Benfro | Keeston WwTW | 5002 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194277 | 215067 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JH | SA611JH | sa61 1jh | sa611jh | Pembrokeshire | Sir Benfro | Keeston WwTW | 5632 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194727 | 214625 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JJ | SA611JJ | sa61 1jj | sa611jj | Pembrokeshire | Sir Benfro | Keeston WwTW | 5763 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194738 | 214455 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JL | SA611JL | sa61 1jl | sa611jl | Pembrokeshire | Sir Benfro | Keeston WwTW | 5926 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195096 | 214579 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JN | SA611JN | sa61 1jn | sa611jn | Pembrokeshire | Sir Benfro | Keeston WwTW | 5836 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194881 | 214490 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JP | SA611JP | sa61 1jp | sa611jp | Pembrokeshire | Sir Benfro | Keeston WwTW | 5886 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194767 | 214315 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JS | SA611JS | sa61 1js | sa611js | Pembrokeshire | Sir Benfro | Keeston WwTW | 5954 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194772 | 214228 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JT | SA611JT | sa61 1jt | sa611jt | Pembrokeshire | Sir Benfro | Keeston WwTW | 6071 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194863 | 214152 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JU | SA611JU | sa61 1ju | sa611ju | Pembrokeshire | Sir Benfro | Keeston WwTW | 6109 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194999 | 214226 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JW | SA611JW | sa61 1jw | sa611jw | Pembrokeshire | Sir Benfro | Keeston WwTW | 5916 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194827 | 214329 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JX | SA611JX | sa61 1jx | sa611jx | Pembrokeshire | Sir Benfro | Keeston WwTW | 6162 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195157 | 214305 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LA | SA611LA | sa61 1la | sa611la | Pembrokeshire | Sir Benfro | Keeston WwTW | 6165 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195017 | 214166 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LB | SA611LB | sa61 1lb | sa611lb | Pembrokeshire | Sir Benfro | Keeston WwTW | 6377 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195185 | 214033 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LD | SA611LD | sa61 1ld | sa611ld | Pembrokeshire | Sir Benfro | Keeston WwTW | 6102 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195139 | 214371 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LE | SA611LE | sa61 1le | sa611le | Pembrokeshire | Sir Benfro | Keeston WwTW | 6287 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195351 | 214323 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LG | SA611LG | sa61 1lg | sa611lg | Pembrokeshire | Sir Benfro | Keeston WwTW | 6336 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195480 | 214390 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LH | SA611LH | sa61 1lh | sa611lh | Pembrokeshire | Sir Benfro | Keeston WwTW | 6068 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195139 | 214420 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LJ | SA611LJ | sa61 1lj | sa611lj | Pembrokeshire | Sir Benfro | Keeston WwTW | 6197 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195316 | 214418 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LL | SA611LL | sa61 1ll | sa611ll | Pembrokeshire | Sir Benfro | Keeston WwTW | 6213 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195171 | 214246 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LN | SA611LN | sa61 1ln | sa611ln | Pembrokeshire | Sir Benfro | Keeston WwTW | 6214 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194924 | 214015 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LP | SA611LP | sa61 1lp | sa611lp | Pembrokeshire | Sir Benfro | Keeston WwTW | 6273 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195189 | 214180 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LQ | SA611LQ | sa61 1lq | sa611lq | Pembrokeshire | Sir Benfro | Keeston WwTW | 6472 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195246 | 213960 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LR | SA611LR | sa61 1lr | sa611lr | Pembrokeshire | Sir Benfro | Keeston WwTW | 6102 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194801 | 214057 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LS | SA611LS | sa61 1ls | sa611ls | Pembrokeshire | Sir Benfro | Keeston WwTW | 6390 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195064 | 213904 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LT | SA611LT | sa61 1lt | sa611lt | Pembrokeshire | Sir Benfro | Keeston WwTW | 6425 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195089 | 213879 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LU | SA611LU | sa61 1lu | sa611lu | Pembrokeshire | Sir Benfro | Keeston WwTW | 6483 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195056 | 213773 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LW | SA611LW | sa61 1lw | sa611lw | Pembrokeshire | Sir Benfro | Keeston WwTW | 6214 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194891 | 213987 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LX | SA611LX | sa61 1lx | sa611lx | Pembrokeshire | Sir Benfro | Keeston WwTW | 6511 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195119 | 213791 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LY | SA611LY | sa61 1ly | sa611ly | Pembrokeshire | Sir Benfro | Keeston WwTW | 6486 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195021 | 213740 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LZ | SA611LZ | sa61 1lz | sa611lz | Pembrokeshire | Sir Benfro | Keeston WwTW | 6347 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195021 | 213923 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NA | SA611NA | sa61 1na | sa611na | Pembrokeshire | Sir Benfro | Keeston WwTW | 6366 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195090 | 213960 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NB | SA611NB | sa61 1nb | sa611nb | Pembrokeshire | Sir Benfro | Keeston WwTW | 6587 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195238 | 213796 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1ND | SA611ND | sa61 1nd | sa611nd | Pembrokeshire | Sir Benfro | Keeston WwTW | 6172 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195091 | 214226 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NN | SA611NN | sa61 1nn | sa611nn | Pembrokeshire | Sir Benfro | Keeston WwTW | 6227 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195029 | 214093 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NW | SA611NW | sa61 1nw | sa611nw | Pembrokeshire | Sir Benfro | Keeston WwTW | 6310 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 195082 | 214029 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NY | SA611NY | sa61 1ny | sa611ny | Pembrokeshire | Sir Benfro | Keeston WwTW | 5547 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194948 | 214978 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NZ | SA611NZ | sa61 1nz | sa611nz | Pembrokeshire | Sir Benfro | Keeston WwTW | 5545 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194912 | 214940 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PA | SA611PA | sa61 1pa | sa611pa | Pembrokeshire | Sir Benfro | Keeston WwTW | 5634 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195051 | 214962 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PD | SA611PD | sa61 1pd | sa611pd | Pembrokeshire | Sir Benfro | Keeston WwTW | 5643 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195018 | 214912 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PH | SA611PH | sa61 1ph | sa611ph | Pembrokeshire | Sir Benfro | Keeston WwTW | 5451 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194798 | 214955 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PP | SA611PP | sa61 1pp | sa611pp | Pembrokeshire | Sir Benfro | Keeston WwTW | 5381 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194766 | 215024 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RQ | SA611RQ | sa61 1rq | sa611rq | Pembrokeshire | Sir Benfro | Camrose WwTW | 5949 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195539 | 214925 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RX | SA611RX | sa61 1rx | sa611rx | Pembrokeshire | Sir Benfro | Camrose WwTW | 5890 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195426 | 214927 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RY | SA611RY | sa61 1ry | sa611ry | Pembrokeshire | Sir Benfro | Camrose WwTW | 6038 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195567 | 214838 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SG | SA611SG | sa61 1sg | sa611sg | Pembrokeshire | Sir Benfro | Keeston WwTW | 5844 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195267 | 214891 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SN | SA611SN | sa61 1sn | sa611sn | Pembrokeshire | Sir Benfro | Camrose WwTW | 6027 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195717 | 214942 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SZ | SA611SZ | sa61 1sz | sa611sz | Pembrokeshire | Sir Benfro | Keeston WwTW | 5484 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194495 | 214611 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TJ | SA611TJ | sa61 1tj | sa611tj | Pembrokeshire | Sir Benfro | Camrose WwTW | 5978 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195536 | 214889 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TL | SA611TL | sa61 1tl | sa611tl | Pembrokeshire | Sir Benfro | Keeston WwTW | 5889 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195284 | 214841 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TZ | SA611TZ | sa61 1tz | sa611tz | Pembrokeshire | Sir Benfro | Camrose WwTW | 5884 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 196249 | 215504 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UA | SA611UA | sa61 1ua | sa611ua | Pembrokeshire | Sir Benfro | Camrose WwTW | 5963 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 196370 | 215502 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UE | SA611UE | sa61 1ue | sa611ue | Pembrokeshire | Sir Benfro | Camrose WwTW | 5989 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 196441 | 215529 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UF | SA611UF | sa61 1uf | sa611uf | Pembrokeshire | Sir Benfro | Camrose WwTW | 5939 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 196381 | 215543 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UH | SA611UH | sa61 1uh | sa611uh | Pembrokeshire | Sir Benfro | Camrose WwTW | 6189 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195905 | 214871 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UJ | SA611UJ | sa61 1uj | sa611uj | Pembrokeshire | Sir Benfro | Keeston WwTW | 6590 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 195503 | 214046 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UP | SA611UP | sa61 1up | sa611up | Pembrokeshire | Sir Benfro | Camrose WwTW | 6176 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 196150 | 215057 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UT | SA611UT | sa61 1ut | sa611ut | Pembrokeshire | Sir Benfro | Camrose WwTW | 6312 | 1194 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.25 | 11.87 | 13.12 | 196578 | 215221 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1WR | SA611WR | sa61 1wr | sa611wr | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XA | SA611XA | sa61 1xa | sa611xa | Pembrokeshire | Sir Benfro | Keeston WwTW | 5508 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194723 | 214795 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XB | SA611XB | sa61 1xb | sa611xb | Pembrokeshire | Sir Benfro | Keeston WwTW | 5663 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194613 | 214476 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XD | SA611XD | sa61 1xd | sa611xd | Pembrokeshire | Sir Benfro | Keeston WwTW | 5697 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194537 | 214364 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XE | SA611XE | sa61 1xe | sa611xe | Pembrokeshire | Sir Benfro | Keeston WwTW | 5732 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 194464 | 214257 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XF | SA611XF | sa61 1xf | sa611xf | Pembrokeshire | Sir Benfro | Keeston WwTW | 5749 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194524 | 214285 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XG | SA611XG | sa61 1xg | sa611xg | Pembrokeshire | Sir Benfro | Keeston WwTW | 5850 | 1191 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.2 | 11.84 | 13.09 | 193251 | 213359 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XJ | SA611XJ | sa61 1xj | sa611xj | Pembrokeshire | Sir Benfro | Keeston WwTW | 5901 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194662 | 214203 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XL | SA611XL | sa61 1xl | sa611xl | Pembrokeshire | Sir Benfro | Keeston WwTW | 6534 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 193951 | 212945 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XN | SA611XN | sa61 1xn | sa611xn | Pembrokeshire | Sir Benfro | Keeston WwTW | 5963 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 194681 | 214137 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XQ | SA611XQ | sa61 1xq | sa611xq | Pembrokeshire | Sir Benfro | Keeston WwTW | 5530 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 194202 | 214306 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XR | SA611XR | sa61 1xr | sa611xr | Pembrokeshire | Sir Benfro | Keeston WwTW | 5399 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 193647 | 214080 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XT | SA611XT | sa61 1xt | sa611xt | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XU | SA611XU | sa61 1xu | sa611xu | Pembrokeshire | Sir Benfro | Keeston WwTW | 5577 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194596 | 214578 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1YH | SA611YH | sa61 1yh | sa611yh | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1YQ | SA611YQ | sa61 1yq | sa611yq | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2XA | SA612XA | sa61 2xa | sa612xa | Pembrokeshire | Sir Benfro | Keeston WwTW | 3910 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 192808 | 215314 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 9DT | SA619DT | sa61 9dt | sa619dt | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 9DX | SA619DX | sa61 9dx | sa619dx | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 9EG | SA619EG | sa61 9eg | sa619eg | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 9EL | SA619EL | sa61 9el | sa619el | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 9EN | SA619EN | sa61 9en | sa619en | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 9EP | SA619EP | sa61 9ep | sa619ep | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 9ZZ | SA619ZZ | sa61 9zz | sa619zz | Pembrokeshire | Sir Benfro | Keeston WwTW | 5571 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194644 | 214630 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3AA | SA623AA | sa62 3aa | sa623aa | Pembrokeshire | Sir Benfro | Keeston WwTW | 4682 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 191804 | 214101 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3AB | SA623AB | sa62 3ab | sa623ab | Pembrokeshire | Sir Benfro | Keeston WwTW | 4856 | 1180 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.99 | 11.73 | 12.96 | 191319 | 213848 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3AD | SA623AD | sa62 3ad | sa623ad | Pembrokeshire | Sir Benfro | Keeston WwTW | 5758 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 190327 | 212940 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3BP | SA623BP | sa62 3bp | sa623bp | Pembrokeshire | Sir Benfro | Keeston WwTW | 7760 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193229 | 211302 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3BU | SA623BU | sa62 3bu | sa623bu | Pembrokeshire | Sir Benfro | Keeston WwTW | 6517 | 1191 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.2 | 11.84 | 13.09 | 192529 | 212390 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3BX | SA623BX | sa62 3bx | sa623bx | Pembrokeshire | Sir Benfro | Keeston WwTW | 6452 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 190861 | 212225 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3EJ | SA623EJ | sa62 3ej | sa623ej | Pembrokeshire | Sir Benfro | Keeston WwTW | 8022 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193561 | 211140 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3EL | SA623EL | sa62 3el | sa623el | Pembrokeshire | Sir Benfro | Keeston WwTW | 6005 | 1191 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.2 | 11.84 | 13.09 | 192546 | 212927 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3EN | SA623EN | sa62 3en | sa623en | Pembrokeshire | Sir Benfro | Keeston WwTW | 6195 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 191844 | 212568 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3EP | SA623EP | sa62 3ep | sa623ep | Pembrokeshire | Sir Benfro | Keeston WwTW | 6923 | 1174 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.88 | 11.67 | 12.9 | 191695 | 211810 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3ER | SA623ER | sa62 3er | sa623er | Pembrokeshire | Sir Benfro | Keeston WwTW | 7295 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 191237 | 211394 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3EU | SA623EU | sa62 3eu | sa623eu | Pembrokeshire | Sir Benfro | Keeston WwTW | 8555 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 192865 | 210371 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3EW | SA623EW | sa62 3ew | sa623ew | Pembrokeshire | Sir Benfro | Keeston WwTW | 6499 | 1174 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.88 | 11.67 | 12.9 | 192076 | 212302 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3HA | SA623HA | sa62 3ha | sa623ha | Pembrokeshire | Sir Benfro | Keeston WwTW | 8603 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 193287 | 210437 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3HB | SA623HB | sa62 3hb | sa623hb | Pembrokeshire | Sir Benfro | Keeston WwTW | 8572 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 193204 | 210444 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3HT | SA623HT | sa62 3ht | sa623ht | Pembrokeshire | Sir Benfro | Keeston WwTW | 4562 | 1136 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.17 | 11.29 | 12.48 | 189179 | 214419 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LT | SA623LT | sa62 3lt | sa623lt | Pembrokeshire | Sir Benfro | Keeston WwTW | 4745 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 190091 | 213988 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LY | SA623LY | sa62 3ly | sa623ly | Pembrokeshire | Sir Benfro | Keeston WwTW | 4090 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 188414 | 215366 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3NF | SA623NF | sa62 3nf | sa623nf | Pembrokeshire | Sir Benfro | Keeston WwTW | 8101 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193474 | 211025 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3NU | SA623NU | sa62 3nu | sa623nu | Pembrokeshire | Sir Benfro | Keeston WwTW | 8188 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193311 | 210879 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3NX | SA623NX | sa62 3nx | sa623nx | Pembrokeshire | Sir Benfro | Keeston WwTW | 7142 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 193672 | 212131 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3NY | SA623NY | sa62 3ny | sa623ny | Pembrokeshire | Sir Benfro | Keeston WwTW | 7855 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193517 | 211301 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3NZ | SA623NZ | sa62 3nz | sa623nz | Pembrokeshire | Sir Benfro | Keeston WwTW | 7959 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193419 | 211156 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PA | SA623PA | sa62 3pa | sa623pa | Pembrokeshire | Sir Benfro | Keeston WwTW | 7726 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193336 | 211374 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PB | SA623PB | sa62 3pb | sa623pb | Pembrokeshire | Sir Benfro | Keeston WwTW | 7667 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193342 | 211438 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PD | SA623PD | sa62 3pd | sa623pd | Pembrokeshire | Sir Benfro | Keeston WwTW | 7217 | 1191 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.2 | 11.84 | 13.09 | 192500 | 211659 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PE | SA623PE | sa62 3pe | sa623pe | Pembrokeshire | Sir Benfro | Keeston WwTW | 7839 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193594 | 211347 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PF | SA623PF | sa62 3pf | sa623pf | Pembrokeshire | Sir Benfro | Keeston WwTW | 8024 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193722 | 211198 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PH | SA623PH | sa62 3ph | sa623ph | Pembrokeshire | Sir Benfro | Keeston WwTW | 7900 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193415 | 211217 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PJ | SA623PJ | sa62 3pj | sa623pj | Pembrokeshire | Sir Benfro | Keeston WwTW | 8291 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193369 | 210789 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PL | SA623PL | sa62 3pl | sa623pl | Pembrokeshire | Sir Benfro | Keeston WwTW | 8346 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193203 | 210680 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PN | SA623PN | sa62 3pn | sa623pn | Pembrokeshire | Sir Benfro | Keeston WwTW | 8461 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193185 | 210555 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PP | SA623PP | sa62 3pp | sa623pp | Pembrokeshire | Sir Benfro | Keeston WwTW | 8431 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193246 | 210604 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PQ | SA623PQ | sa62 3pq | sa623pq | Pembrokeshire | Sir Benfro | Keeston WwTW | 8065 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193624 | 211117 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PR | SA623PR | sa62 3pr | sa623pr | Pembrokeshire | Sir Benfro | Keeston WwTW | 8516 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193257 | 210518 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PS | SA623PS | sa62 3ps | sa623ps | Pembrokeshire | Sir Benfro | Keeston WwTW | 8555 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193497 | 210553 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PW | SA623PW | sa62 3pw | sa623pw | Pembrokeshire | Sir Benfro | Keeston WwTW | 8435 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193095 | 210556 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PX | SA623PX | sa62 3px | sa623px | Pembrokeshire | Sir Benfro | Keeston WwTW | 8619 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193544 | 210501 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PY | SA623PY | sa62 3py | sa623py | Pembrokeshire | Sir Benfro | Keeston WwTW | 8677 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193992 | 210602 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3PZ | SA623PZ | sa62 3pz | sa623pz | Pembrokeshire | Sir Benfro | Keeston WwTW | 8333 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193291 | 210720 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3QE | SA623QE | sa62 3qe | sa623qe | Pembrokeshire | Sir Benfro | Keeston WwTW | 8254 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193511 | 210876 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3QF | SA623QF | sa62 3qf | sa623qf | Pembrokeshire | Sir Benfro | Keeston WwTW | 7977 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193520 | 211173 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3QG | SA623QG | sa62 3qg | sa623qg | Pembrokeshire | Sir Benfro | Keeston WwTW | 8454 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193433 | 210638 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3QH | SA623QH | sa62 3qh | sa623qh | Pembrokeshire | Sir Benfro | Keeston WwTW | 8208 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193475 | 210912 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3QJ | SA623QJ | sa62 3qj | sa623qj | Pembrokeshire | Sir Benfro | Keeston WwTW | 8230 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193258 | 210818 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3QL | SA623QL | sa62 3ql | sa623ql | Pembrokeshire | Sir Benfro | Keeston WwTW | 8005 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193581 | 211165 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3QN | SA623QN | sa62 3qn | sa623qn | Pembrokeshire | Sir Benfro | Keeston WwTW | 7891 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193534 | 211269 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3QP | SA623QP | sa62 3qp | sa623qp | Pembrokeshire | Sir Benfro | Keeston WwTW | 6625 | 1161 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.64 | 11.54 | 12.76 | 190078 | 212093 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3QQ | SA623QQ | sa62 3qq | sa623qq | Pembrokeshire | Sir Benfro | Keeston WwTW | 8456 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 193380 | 210619 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3QT | SA623QT | sa62 3qt | sa623qt | Pembrokeshire | Sir Benfro | Keeston WwTW | 8198 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193508 | 210934 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3QW | SA623QW | sa62 3qw | sa623qw | Pembrokeshire | Sir Benfro | Keeston WwTW | 8562 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 193647 | 210597 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3SA | SA623SA | sa62 3sa | sa623sa | Pembrokeshire | Sir Benfro | Keeston WwTW | 6026 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 189982 | 212709 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3TS | SA623TS | sa62 3ts | sa623ts | Pembrokeshire | Sir Benfro | Keeston WwTW | 5218 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 192296 | 213674 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3TU | SA623TU | sa62 3tu | sa623tu | Pembrokeshire | Sir Benfro | Keeston WwTW | 6013 | 1121 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.89 | 11.14 | 12.32 | 188155 | 213284 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3XG | SA623XG | sa62 3xg | sa623xg | Pembrokeshire | Sir Benfro | Keeston WwTW | 4585 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 192131 | 214285 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3XH | SA623XH | sa62 3xh | sa623xh | Pembrokeshire | Sir Benfro | Keeston WwTW | 4571 | 1187 | 900to1200 | 2.38 | 1.74 | 1.27 | 22.12 | 11.8 | 13.04 | 192570 | 214457 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4AA | SA624AA | sa62 4aa | sa624aa | Pembrokeshire | Sir Benfro | Wiston STW | 6533 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 196962 | 214442 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4AB | SA624AB | sa62 4ab | sa624ab | Pembrokeshire | Sir Benfro | Wiston STW | 6460 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 197031 | 214470 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4AD | SA624AD | sa62 4ad | sa624ad | Pembrokeshire | Sir Benfro | Wiston STW | 5842 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 197505 | 214887 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4AE | SA624AE | sa62 4ae | sa624ae | Pembrokeshire | Sir Benfro | Wiston STW | 6428 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 197220 | 214222 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4AG | SA624AG | sa62 4ag | sa624ag | Pembrokeshire | Sir Benfro | Wiston STW | 6392 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 197398 | 214023 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AH | SA624AH | sa62 4ah | sa624ah | Pembrokeshire | Sir Benfro | Wiston STW | 6153 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 198603 | 213049 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AJ | SA624AJ | sa62 4aj | sa624aj | Pembrokeshire | Sir Benfro | Wiston STW | 5099 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 199064 | 214055 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AL | SA624AL | sa62 4al | sa624al | Pembrokeshire | Sir Benfro | Wiston STW | 4848 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 199504 | 213996 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AN | SA624AN | sa62 4an | sa624an | Pembrokeshire | Sir Benfro | Wiston STW | 4186 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 199762 | 214651 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AP | SA624AP | sa62 4ap | sa624ap | Pembrokeshire | Sir Benfro | Wiston STW | 5192 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 199569 | 213509 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AQ | SA624AQ | sa62 4aq | sa624aq | Pembrokeshire | Sir Benfro | Wiston STW | 7143 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 197545 | 212683 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AR | SA624AR | sa62 4ar | sa624ar | Pembrokeshire | Sir Benfro | Wiston STW | 5407 | 1220 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.74 | 12.13 | 13.4 | 200550 | 212714 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AS | SA624AS | sa62 4as | sa624as | Pembrokeshire | Sir Benfro | Wiston STW | 4379 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 201070 | 213614 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AT | SA624AT | sa62 4at | sa624at | Pembrokeshire | Sir Benfro | Wiston STW | 3913 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 200710 | 214295 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AU | SA624AU | sa62 4au | sa624au | Pembrokeshire | Sir Benfro | Wiston STW | 3842 | 1221 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.76 | 12.14 | 13.41 | 200757 | 214349 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AW | SA624AW | sa62 4aw | sa624aw | Pembrokeshire | Sir Benfro | Wiston STW | 3606 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 200254 | 214988 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4AX | SA624AX | sa62 4ax | sa624ax | Pembrokeshire | Sir Benfro | Wiston STW | 3323 | 1220 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.74 | 12.13 | 13.4 | 201775 | 214496 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AY | SA624AY | sa62 4ay | sa624ay | Pembrokeshire | Sir Benfro | Wiston STW | 2776 | 1269 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.65 | 12.61 | 13.94 | 202251 | 214958 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AZ | SA624AZ | sa62 4az | sa624az | Pembrokeshire | Sir Benfro | Keeston WwTW | 9073 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 195956 | 211201 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BA | SA624BA | sa62 4ba | sa624ba | Pembrokeshire | Sir Benfro | Wiston STW | 2418 | 1269 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.65 | 12.61 | 13.94 | 201657 | 215492 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BD | SA624BD | sa62 4bd | sa624bd | Pembrokeshire | Sir Benfro | Wiston STW | 2608 | 1248 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.26 | 12.41 | 13.71 | 200507 | 216181 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BE | SA624BE | sa62 4be | sa624be | Pembrokeshire | Sir Benfro | Wiston STW | 2084 | 1249 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.28 | 12.42 | 13.72 | 200693 | 216915 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EA | SA624EA | sa62 4ea | sa624ea | Pembrokeshire | Sir Benfro | Keeston WwTW | 8833 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 195444 | 211154 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4ES | SA624ES | sa62 4es | sa624es | Pembrokeshire | Sir Benfro | Wiston STW | 7045 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 196846 | 213672 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4ET | SA624ET | sa62 4et | sa624et | Pembrokeshire | Sir Benfro | Keeston WwTW | 8288 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 196051 | 212252 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EU | SA624EU | sa62 4eu | sa624eu | Pembrokeshire | Sir Benfro | Keeston WwTW | 8883 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 195645 | 211222 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EX | SA624EX | sa62 4ex | sa624ex | Pembrokeshire | Sir Benfro | Keeston WwTW | 8794 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 195489 | 211228 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EY | SA624EY | sa62 4ey | sa624ey | Pembrokeshire | Sir Benfro | Keeston WwTW | 8847 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 195103 | 210938 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4FB | SA624FB | sa62 4fb | sa624fb | Pembrokeshire | Sir Benfro | Keeston WwTW | 8971 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 195721 | 211166 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HA | SA624HA | sa62 4ha | sa624ha | Pembrokeshire | Sir Benfro | Keeston WwTW | 9021 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 195831 | 211179 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HB | SA624HB | sa62 4hb | sa624hb | Pembrokeshire | Sir Benfro | Keeston WwTW | 9649 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 196075 | 210587 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HD | SA624HD | sa62 4hd | sa624hd | Pembrokeshire | Sir Benfro | Keeston WwTW | 9559 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 195720 | 210472 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HE | SA624HE | sa62 4he | sa624he | Pembrokeshire | Sir Benfro | Wiston STW | 9871 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 196222 | 210192 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HG | SA624HG | sa62 4hg | sa624hg | Pembrokeshire | Sir Benfro | Wiston STW | 8888 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 198751 | 209707 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HH | SA624HH | sa62 4hh | sa624hh | Pembrokeshire | Sir Benfro | Wiston STW | 8902 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 198973 | 209589 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HJ | SA624HJ | sa62 4hj | sa624hj | Pembrokeshire | Sir Benfro | Wiston STW | 8741 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 198906 | 209796 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HL | SA624HL | sa62 4hl | sa624hl | Pembrokeshire | Sir Benfro | Wiston STW | 8371 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 198965 | 210178 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4HN | SA624HN | sa62 4hn | sa624hn | Pembrokeshire | Sir Benfro | Wiston STW | 8605 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 199836 | 209567 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4HP | SA624HP | sa62 4hp | sa624hp | Pembrokeshire | Sir Benfro | Wiston STW | 8948 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 198939 | 209553 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HR | SA624HR | sa62 4hr | sa624hr | Pembrokeshire | Sir Benfro | Wiston STW | 8969 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199031 | 209490 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HS | SA624HS | sa62 4hs | sa624hs | Pembrokeshire | Sir Benfro | Wiston STW | 8974 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199069 | 209468 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HT | SA624HT | sa62 4ht | sa624ht | Pembrokeshire | Sir Benfro | Wiston STW | 9001 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199131 | 209412 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HU | SA624HU | sa62 4hu | sa624hu | Pembrokeshire | Sir Benfro | Wiston STW | 9036 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 198972 | 209442 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HW | SA624HW | sa62 4hw | sa624hw | Pembrokeshire | Sir Benfro | Wiston STW | 8738 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 198848 | 209827 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HX | SA624HX | sa62 4hx | sa624hx | Pembrokeshire | Sir Benfro | Wiston STW | 9097 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199000 | 209363 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HY | SA624HY | sa62 4hy | sa624hy | Pembrokeshire | Sir Benfro | Wiston STW | 9176 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 198869 | 209335 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JA | SA624JA | sa62 4ja | sa624ja | Pembrokeshire | Sir Benfro | Wiston STW | 9057 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199279 | 209291 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JB | SA624JB | sa62 4jb | sa624jb | Pembrokeshire | Sir Benfro | Wiston STW | 8976 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199450 | 209312 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JD | SA624JD | sa62 4jd | sa624jd | Pembrokeshire | Sir Benfro | Wiston STW | 8820 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 199588 | 209427 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JE | SA624JE | sa62 4je | sa624je | Pembrokeshire | Sir Benfro | Wiston STW | 9154 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199004 | 209300 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JF | SA624JF | sa62 4jf | sa624jf | Pembrokeshire | Sir Benfro | Wiston STW | 8982 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199292 | 209366 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JG | SA624JG | sa62 4jg | sa624jg | Pembrokeshire | Sir Benfro | Wiston STW | 9176 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199078 | 209244 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JH | SA624JH | sa62 4jh | sa624jh | Pembrokeshire | Sir Benfro | Wiston STW | 9216 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199122 | 209183 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JJ | SA624JJ | sa62 4jj | sa624jj | Pembrokeshire | Sir Benfro | Wiston STW | 9200 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199183 | 209175 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JL | SA624JL | sa62 4jl | sa624jl | Pembrokeshire | Sir Benfro | Wiston STW | 9233 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199206 | 209131 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JN | SA624JN | sa62 4jn | sa624jn | Pembrokeshire | Sir Benfro | Wiston STW | 9312 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 199592 | 208903 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JP | SA624JP | sa62 4jp | sa624jp | Pembrokeshire | Sir Benfro | Wiston STW | 9279 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199043 | 209147 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JQ | SA624JQ | sa62 4jq | sa624jq | Pembrokeshire | Sir Benfro | Wiston STW | 9981 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 199003 | 208406 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JR | SA624JR | sa62 4jr | sa624jr | Pembrokeshire | Sir Benfro | Wiston STW | 9651 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 198909 | 208800 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JS | SA624JS | sa62 4js | sa624js | Pembrokeshire | Sir Benfro | Wiston STW | 10099 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 198598 | 208446 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JT | SA624JT | sa62 4jt | sa624jt | Pembrokeshire | Sir Benfro | Wiston STW | 9874 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199017 | 208516 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JU | SA624JU | sa62 4ju | sa624ju | Pembrokeshire | Sir Benfro | Wiston STW | 7795 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 197719 | 211647 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JW | SA624JW | sa62 4jw | sa624jw | Pembrokeshire | Sir Benfro | Wiston STW | 9309 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 199119 | 209084 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LA | SA624LA | sa62 4la | sa624la | Pembrokeshire | Sir Benfro | Keeston WwTW | 6733 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 195009 | 213410 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LB | SA624LB | sa62 4lb | sa624lb | Pembrokeshire | Sir Benfro | Keeston WwTW | 7735 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 195516 | 212534 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LD | SA624LD | sa62 4ld | sa624ld | Pembrokeshire | Sir Benfro | Keeston WwTW | 8680 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 195744 | 211532 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LE | SA624LE | sa62 4le | sa624le | Pembrokeshire | Sir Benfro | Keeston WwTW | 8586 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 195441 | 211444 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LF | SA624LF | sa62 4lf | sa624lf | Pembrokeshire | Sir Benfro | Wiston STW | 8054 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 198058 | 211072 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LG | SA624LG | sa62 4lg | sa624lg | Pembrokeshire | Sir Benfro | Keeston WwTW | 8869 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 195807 | 211346 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LH | SA624LH | sa62 4lh | sa624lh | Pembrokeshire | Sir Benfro | Wiston STW | 8374 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 197092 | 211419 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4LJ | SA624LJ | sa62 4lj | sa624lj | Pembrokeshire | Sir Benfro | Wiston STW | 8336 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 197198 | 211377 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LL | SA624LL | sa62 4ll | sa624ll | Pembrokeshire | Sir Benfro | Wiston STW | 7895 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 197746 | 211498 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LN | SA624LN | sa62 4ln | sa624ln | Pembrokeshire | Sir Benfro | Wiston STW | 7987 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 197672 | 211439 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LP | SA624LP | sa62 4lp | sa624lp | Pembrokeshire | Sir Benfro | Wiston STW | 7938 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 197727 | 211459 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LQ | SA624LQ | sa62 4lq | sa624lq | Pembrokeshire | Sir Benfro | Wiston STW | 8932 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 196348 | 211350 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LR | SA624LR | sa62 4lr | sa624lr | Pembrokeshire | Sir Benfro | Wiston STW | 7304 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 198286 | 211830 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LS | SA624LS | sa62 4ls | sa624ls | Pembrokeshire | Sir Benfro | Wiston STW | 8006 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 197789 | 211325 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LT | SA624LT | sa62 4lt | sa624lt | Pembrokeshire | Sir Benfro | Wiston STW | 8000 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 197935 | 211225 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LU | SA624LU | sa62 4lu | sa624lu | Pembrokeshire | Sir Benfro | Wiston STW | 7798 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 198365 | 211174 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LW | SA624LW | sa62 4lw | sa624lw | Pembrokeshire | Sir Benfro | Wiston STW | 7893 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 198267 | 211125 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LX | SA624LX | sa62 4lx | sa624lx | Pembrokeshire | Sir Benfro | Wiston STW | 7755 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 198391 | 211209 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LY | SA624LY | sa62 4ly | sa624ly | Pembrokeshire | Sir Benfro | Wiston STW | 7822 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 198190 | 211262 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LZ | SA624LZ | sa62 4lz | sa624lz | Pembrokeshire | Sir Benfro | Wiston STW | 7917 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 198199 | 211141 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NA | SA624NA | sa62 4na | sa624na | Pembrokeshire | Sir Benfro | Wiston STW | 7806 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 198404 | 211140 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NB | SA624NB | sa62 4nb | sa624nb | Pembrokeshire | Sir Benfro | Wiston STW | 8123 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 197970 | 211049 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4ND | SA624ND | sa62 4nd | sa624nd | Pembrokeshire | Sir Benfro | Wiston STW | 8210 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 197907 | 210986 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NE | SA624NE | sa62 4ne | sa624ne | Pembrokeshire | Sir Benfro | Wiston STW | 8206 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 197944 | 210966 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NF | SA624NF | sa62 4nf | sa624nf | Pembrokeshire | Sir Benfro | Wiston STW | 7927 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 197831 | 211392 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NG | SA624NG | sa62 4ng | sa624ng | Pembrokeshire | Sir Benfro | Wiston STW | 8402 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 198450 | 210415 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NH | SA624NH | sa62 4nh | sa624nh | Pembrokeshire | Sir Benfro | Wiston STW | 9254 | 1226 | 1200to1500 | 2.45 | 1.8 | 1.32 | 22.85 | 12.19 | 13.47 | 197386 | 210077 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NN | SA624NN | sa62 4nn | sa624nn | Pembrokeshire | Sir Benfro | Keeston WwTW | 9537 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 195590 | 210421 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NP | SA624NP | sa62 4np | sa624np | Pembrokeshire | Sir Benfro | Wiston STW | 9991 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 197028 | 209430 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NQ | SA624NQ | sa62 4nq | sa624nq | Pembrokeshire | Sir Benfro | Wiston STW | 10434 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 198018 | 208345 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NR | SA624NR | sa62 4nr | sa624nr | Pembrokeshire | Sir Benfro | Wiston STW | 10405 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 197123 | 208874 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NS | SA624NS | sa62 4ns | sa624ns | Pembrokeshire | Sir Benfro | Wiston STW | 10551 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 197361 | 208562 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NT | SA624NT | sa62 4nt | sa624nt | Pembrokeshire | Sir Benfro | Wiston STW | 9997 | 1211 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.57 | 12.04 | 13.31 | 197918 | 208887 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NU | SA624NU | sa62 4nu | sa624nu | Pembrokeshire | Sir Benfro | Wiston STW | 10408 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 197945 | 208410 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NW | SA624NW | sa62 4nw | sa624nw | Pembrokeshire | Sir Benfro | Wiston STW | 10474 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 197889 | 208364 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NX | SA624NX | sa62 4nx | sa624nx | Pembrokeshire | Sir Benfro | Wiston STW | 9605 | 1211 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.57 | 12.04 | 13.31 | 198457 | 209053 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NY | SA624NY | sa62 4ny | sa624ny | Pembrokeshire | Sir Benfro | Wiston STW | 8109 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 197949 | 211081 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NZ | SA624NZ | sa62 4nz | sa624nz | Pembrokeshire | Sir Benfro | Wiston STW | 8010 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 197717 | 211375 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PA | SA624PA | sa62 4pa | sa624pa | Pembrokeshire | Sir Benfro | Wiston STW | 5061 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 198122 | 215389 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PB | SA624PB | sa62 4pb | sa624pb | Pembrokeshire | Sir Benfro | Wiston STW | 4052 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 198995 | 215898 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PD | SA624PD | sa62 4pd | sa624pd | Pembrokeshire | Sir Benfro | Wiston STW | 2099 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 202769 | 215616 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PE | SA624PE | sa62 4pe | sa624pe | Pembrokeshire | Sir Benfro | Wiston STW | 3054 | 1283 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.91 | 12.75 | 14.1 | 204131 | 215056 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4PF | SA624PF | sa62 4pf | sa624pf | Pembrokeshire | Sir Benfro | Wiston STW | 8334 | 1192 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.22 | 11.85 | 13.1 | 197249 | 211336 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PG | SA624PG | sa62 4pg | sa624pg | Pembrokeshire | Sir Benfro | Wiston STW | 1780 | 1288 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.01 | 12.8 | 14.15 | 203527 | 216178 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6YT | SA626YT | sa62 6yt | sa626yt | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8AA | SA678AA | sa67 8aa | sa678aa | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3320 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 205787 | 213930 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA67 8AB | SA678AB | sa67 8ab | sa678ab | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 4192 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 205674 | 212781 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8AD | SA678AD | sa67 8ad | sa678ad | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 4492 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 206353 | 211957 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8AP | SA678AP | sa67 8ap | sa678ap | Pembrokeshire | Sir Benfro | Wiston STW | 7181 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 203596 | 210595 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8AR | SA678AR | sa67 8ar | sa678ar | Pembrokeshire | Sir Benfro | Wiston STW | 6986 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 203532 | 210783 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8AS | SA678AS | sa67 8as | sa678as | Pembrokeshire | Sir Benfro | Wiston STW | 7144 | 1232 | 1200to1500 | 2.47 | 1.8 | 1.32 | 22.96 | 12.25 | 13.54 | 203072 | 210580 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8AT | SA678AT | sa67 8at | sa678at | Pembrokeshire | Sir Benfro | Wiston STW | 7315 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 202520 | 210395 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8AU | SA678AU | sa67 8au | sa678au | Pembrokeshire | Sir Benfro | Wiston STW | 7426 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 202213 | 210295 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA67 8AW | SA678AW | sa67 8aw | sa678aw | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 8153 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 203445 | 209488 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8AX | SA678AX | sa67 8ax | sa678ax | Pembrokeshire | Sir Benfro | Wiston STW | 7889 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 202437 | 209822 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8AY | SA678AY | sa67 8ay | sa678ay | Pembrokeshire | Sir Benfro | Wiston STW | 8601 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 202743 | 209109 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA67 8AZ | SA678AZ | sa67 8az | sa678az | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 8538 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 203226 | 209170 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8BA | SA678BA | sa67 8ba | sa678ba | Pembrokeshire | Sir Benfro | Wiston STW | 8291 | 1208 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.52 | 12.01 | 13.27 | 201606 | 209481 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA67 8BB | SA678BB | sa67 8bb | sa678bb | Pembrokeshire | Sir Benfro | Wiston STW | 7263 | 1225 | 1200to1500 | 2.45 | 1.79 | 1.32 | 22.83 | 12.18 | 13.46 | 202218 | 210458 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA67 8BD | SA678BD | sa67 8bd | sa678bd | Pembrokeshire | Sir Benfro | Wiston STW | 6821 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 202016 | 210915 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA67 8BE | SA678BE | sa67 8be | sa678be | Pembrokeshire | Sir Benfro | Wiston STW | 6597 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 201001 | 211314 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA67 8BG | SA678BG | sa67 8bg | sa678bg | Pembrokeshire | Sir Benfro | Wiston STW | 6495 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 202176 | 211230 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8BH | SA678BH | sa67 8bh | sa678bh | Pembrokeshire | Sir Benfro | Wiston STW | 6196 | 1252 | 1200to1500 | 2.51 | 1.83 | 1.34 | 23.34 | 12.45 | 13.76 | 203134 | 211535 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8BJ | SA678BJ | sa67 8bj | sa678bj | Pembrokeshire | Sir Benfro | Wiston STW | 4946 | 1279 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.84 | 12.71 | 14.05 | 203975 | 212953 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA67 8BL | SA678BL | sa67 8bl | sa678bl | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2798 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 206104 | 214385 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA67 8DB | SA678DB | sa67 8db | sa678db | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3960 | 1312 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.45 | 13.04 | 14.41 | 207460 | 212100 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DD | SA678DD | sa67 8dd | sa678dd | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 4045 | 1312 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.45 | 13.04 | 14.41 | 207191 | 212089 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DZ | SA678DZ | sa67 8dz | sa678dz | Pembrokeshire | Sir Benfro | Wiston STW | 1726 | 1288 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.01 | 12.8 | 14.15 | 203641 | 216318 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0PL | SA680PL | sa68 0pl | sa680pl | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 9557 | 1226 | 1200to1500 | 2.45 | 1.8 | 1.32 | 22.85 | 12.19 | 13.47 | 204203 | 207368 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA68 0PN | SA680PN | sa68 0pn | sa680pn | Pembrokeshire | Sir Benfro | Wiston STW | 10779 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 201815 | 206960 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA68 0PP | SA680PP | sa68 0pp | sa680pp | Pembrokeshire | Sir Benfro | Wiston STW | 10869 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 201779 | 206873 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA68 0PR | SA680PR | sa68 0pr | sa680pr | Pembrokeshire | Sir Benfro | Wiston STW | 11603 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 201156 | 206199 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA68 0PS | SA680PS | sa68 0ps | sa680ps | Pembrokeshire | Sir Benfro | Wiston STW | 10657 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 202189 | 207061 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA68 0PT | SA680PT | sa68 0pt | sa680pt | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 9589 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 203008 | 208030 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA68 0PU | SA680PU | sa68 0pu | sa680pu | Pembrokeshire | Sir Benfro | Wiston STW | 9959 | 1194 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.25 | 11.87 | 13.12 | 201984 | 207771 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA68 0PW | SA680PW | sa68 0pw | sa680pw | Pembrokeshire | Sir Benfro | Wiston STW | 10731 | 1203 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.42 | 11.96 | 13.22 | 201712 | 207017 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA68 0PX | SA680PX | sa68 0px | sa680px | Pembrokeshire | Sir Benfro | Wiston STW | 9328 | 1194 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.25 | 11.87 | 13.12 | 202219 | 208390 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA68 0PY | SA680PY | sa68 0py | sa680py | Pembrokeshire | Sir Benfro | Wiston STW | 9075 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 200986 | 208783 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA68 0QA | SA680QA | sa68 0qa | sa680qa | Pembrokeshire | Sir Benfro | Wiston STW | 9295 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 200175 | 208742 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 1LA | SA731LA | sa73 1la | sa731la | Pembrokeshire | Sir Benfro | Wiston STW | 10654 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 197012 | 208650 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LB | SA731LB | sa73 1lb | sa731lb | Pembrokeshire | Sir Benfro | Wiston STW | 11302 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 196570 | 208162 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LD | SA731LD | sa73 1ld | sa731ld | Pembrokeshire | Sir Benfro | Wiston STW | 11276 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 197278 | 207779 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LE | SA731LE | sa73 1le | sa731le | Pembrokeshire | Sir Benfro | Wiston STW | 12156 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 196745 | 207067 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LG | SA731LG | sa73 1lg | sa731lg | Pembrokeshire | Sir Benfro | Wiston STW | 12335 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 197144 | 206656 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LH | SA731LH | sa73 1lh | sa731lh | Pembrokeshire | Sir Benfro | Wiston STW | 11967 | 1174 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.88 | 11.67 | 12.9 | 196177 | 207624 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LR | SA731LR | sa73 1lr | sa731lr | Pembrokeshire | Sir Benfro | Wiston STW | 12878 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 198376 | 205550 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LU | SA731LU | sa73 1lu | sa731lu | Pembrokeshire | Sir Benfro | Wiston STW | 10577 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 196907 | 208807 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LW | SA731LW | sa73 1lw | sa731lw | Pembrokeshire | Sir Benfro | Wiston STW | 12940 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 198540 | 205429 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LX | SA731LX | sa73 1lx | sa731lx | Pembrokeshire | Sir Benfro | Wiston STW | 10543 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 197043 | 208762 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LY | SA731LY | sa73 1ly | sa731ly | Pembrokeshire | Sir Benfro | Wiston STW | 10572 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 197251 | 208602 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LZ | SA731LZ | sa73 1lz | sa731lz | Pembrokeshire | Sir Benfro | Wiston STW | 10508 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 197039 | 208805 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NA | SA731NA | sa73 1na | sa731na | Pembrokeshire | Sir Benfro | Wiston STW | 10586 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 197552 | 208415 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NB | SA731NB | sa73 1nb | sa731nb | Pembrokeshire | Sir Benfro | Wiston STW | 10556 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 197878 | 208278 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1ND | SA731ND | sa73 1nd | sa731nd | Pembrokeshire | Sir Benfro | Wiston STW | 10632 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 198276 | 208005 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NE | SA731NE | sa73 1ne | sa731ne | Pembrokeshire | Sir Benfro | Wiston STW | 10861 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 198272 | 207756 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NF | SA731NF | sa73 1nf | sa731nf | Pembrokeshire | Sir Benfro | Wiston STW | 10337 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 199231 | 207943 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 1NG | SA731NG | sa73 1ng | sa731ng | Pembrokeshire | Sir Benfro | Wiston STW | 10409 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 198384 | 208201 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 1NH | SA731NH | sa73 1nh | sa731nh | Pembrokeshire | Sir Benfro | Wiston STW | 10622 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 198355 | 207981 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NJ | SA731NJ | sa73 1nj | sa731nj | Pembrokeshire | Sir Benfro | Wiston STW | 10951 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 198505 | 207561 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 1NL | SA731NL | sa73 1nl | sa731nl | Pembrokeshire | Sir Benfro | Wiston STW | 11332 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 198717 | 207070 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 1NN | SA731NN | sa73 1nn | sa731nn | Pembrokeshire | Sir Benfro | Wiston STW | 11223 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 198288 | 207356 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NP | SA731NP | sa73 1np | sa731np | Pembrokeshire | Sir Benfro | Wiston STW | 11297 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 198359 | 207246 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NQ | SA731NQ | sa73 1nq | sa731nq | Pembrokeshire | Sir Benfro | Wiston STW | 11407 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 198292 | 207155 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NR | SA731NR | sa73 1nr | sa731nr | Pembrokeshire | Sir Benfro | Wiston STW | 11470 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 198342 | 207066 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NS | SA731NS | sa73 1ns | sa731ns | Pembrokeshire | Sir Benfro | Wiston STW | 11967 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 198223 | 206579 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NT | SA731NT | sa73 1nt | sa731nt | Pembrokeshire | Sir Benfro | Wiston STW | 13027 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 198335 | 205407 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NU | SA731NU | sa73 1nu | sa731nu | Pembrokeshire | Sir Benfro | Wiston STW | 12907 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 198476 | 205485 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NW | SA731NW | sa73 1nw | sa731nw | Pembrokeshire | Sir Benfro | Wiston STW | 11339 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 198316 | 207218 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NX | SA731NX | sa73 1nx | sa731nx | Pembrokeshire | Sir Benfro | Wiston STW | 13374 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 198170 | 205097 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NY | SA731NY | sa73 1ny | sa731ny | Pembrokeshire | Sir Benfro | Wiston STW | 13466 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 198174 | 204998 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NZ | SA731NZ | sa73 1nz | sa731nz | Pembrokeshire | Sir Benfro | Wiston STW | 12994 | 1176 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.92 | 11.69 | 12.92 | 198520 | 205379 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PA | SA731PA | sa73 1pa | sa731pa | Pembrokeshire | Sir Benfro | Wiston STW | 13405 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 197666 | 205253 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PB | SA731PB | sa73 1pb | sa731pb | Pembrokeshire | Sir Benfro | Wiston STW | 13534 | 1145 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.34 | 11.38 | 12.58 | 197233 | 205293 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PD | SA731PD | sa73 1pd | sa731pd | Pembrokeshire | Sir Benfro | Wiston STW | 12129 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 199419 | 206010 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 1PE | SA731PE | sa73 1pe | sa731pe | Pembrokeshire | Sir Benfro | Wiston STW | 11459 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 199793 | 206604 | Pembrokeshire Coast National Park LPA | PE |  | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 1PF | SA731PF | sa73 1pf | sa731pf | Pembrokeshire | Sir Benfro | Wiston STW | 13606 | 1145 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.34 | 11.38 | 12.58 | 197039 | 205300 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PG | SA731PG | sa73 1pg | sa731pg | Pembrokeshire | Sir Benfro | Wiston STW | 13017 | 1181 | 900to1200 | 2.36 | 1.73 | 1.27 | 22.01 | 11.74 | 12.98 | 198261 | 205443 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PQ | SA731PQ | sa73 1pq | sa731pq | Pembrokeshire | Sir Benfro | Wiston STW | 11254 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 198194 | 207362 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3JD | SA733JD | sa73 3jd | sa733jd | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 9AP | SA739AP | sa73 9ap | sa739ap | Pembrokeshire | Sir Benfro | Keeston WwTW | 5573 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194650 | 214633 | Pembrokeshire LPA | PE |  | Cyngor Sir Penfro | Pembrokeshire County Council
SA14 6AA | SA146AA | sa14 6aa | sa146aa | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1607 | Over1500 | 3.2165 | 2.3535 | 1.7259 | 29.952 | 15.9744 | 17.6559 | 253956 | 208414 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AB | SA146AB | sa14 6ab | sa146ab | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1607 | Over1500 | 3.2165 | 2.3535 | 1.7259 | 29.952 | 15.9744 | 17.6559 | 253894 | 208433 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AD | SA146AD | sa14 6ad | sa146ad | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1607 | Over1500 | 3.2165 | 2.3535 | 1.7259 | 29.952 | 15.9744 | 17.6559 | 253949 | 208632 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AE | SA146AE | sa14 6ae | sa146ae | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 254163 | 208718 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AF | SA146AF | sa14 6af | sa146af | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1613 | Over1500 | 3.2285 | 2.3623 | 1.7324 | 30.0638 | 16.034 | 17.7218 | 254481 | 209508 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AG | SA146AG | sa14 6ag | sa146ag | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1613 | Over1500 | 3.2285 | 2.3623 | 1.7324 | 30.0638 | 16.034 | 17.7218 | 254194 | 209531 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AH | SA146AH | sa14 6ah | sa146ah | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1613 | Over1500 | 3.2285 | 2.3623 | 1.7324 | 30.0638 | 16.034 | 17.7218 | 254370 | 209920 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AL | SA146AL | sa14 6al | sa146al | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1569 | Over1500 | 3.1404 | 2.2979 | 1.6851 | 29.2437 | 15.5966 | 17.2384 | 254001 | 209126 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AN | SA146AN | sa14 6an | sa146an | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1569 | Over1500 | 3.1404 | 2.2979 | 1.6851 | 29.2437 | 15.5966 | 17.2384 | 253982 | 209084 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AP | SA146AP | sa14 6ap | sa146ap | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1569 | Over1500 | 3.1404 | 2.2979 | 1.6851 | 29.2437 | 15.5966 | 17.2384 | 253796 | 209549 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AQ | SA146AQ | sa14 6aq | sa146aq | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1565 | Over1500 | 3.1324 | 2.292 | 1.6808 | 29.1691 | 15.5569 | 17.1944 | 257793 | 211394 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AW | SA146AW | sa14 6aw | sa146aw | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1613 | Over1500 | 3.2285 | 2.3623 | 1.7324 | 30.0638 | 16.034 | 17.7218 | 254025 | 209527 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AX | SA146AX | sa14 6ax | sa146ax | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 254065 | 208822 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AY | SA146AY | sa14 6ay | sa146ay | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1515 | Over1500 | 3.0323 | 2.2188 | 1.6271 | 28.2372 | 15.0599 | 16.6451 | 253813 | 207769 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6AZ | SA146AZ | sa14 6az | sa146az | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1607 | Over1500 | 3.2165 | 2.3535 | 1.7259 | 29.952 | 15.9744 | 17.6559 | 253954 | 208332 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6BA | SA146BA | sa14 6ba | sa146ba | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1607 | Over1500 | 3.2165 | 2.3535 | 1.7259 | 29.952 | 15.9744 | 17.6559 | 253732 | 208007 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6BB | SA146BB | sa14 6bb | sa146bb | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1515 | Over1500 | 3.0323 | 2.2188 | 1.6271 | 28.2372 | 15.0599 | 16.6451 | 253513 | 207944 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6BD | SA146BD | sa14 6bd | sa146bd | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1607 | Over1500 | 3.2165 | 2.3535 | 1.7259 | 29.952 | 15.9744 | 17.6559 | 253924 | 208203 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6BE | SA146BE | sa14 6be | sa146be | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1607 | Over1500 | 3.2165 | 2.3535 | 1.7259 | 29.952 | 15.9744 | 17.6559 | 253975 | 208379 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6BG | SA146BG | sa14 6bg | sa146bg | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 254040 | 208672 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6BH | SA146BH | sa14 6bh | sa146bh | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1515 | Over1500 | 3.0323 | 2.2188 | 1.6271 | 28.2372 | 15.0599 | 16.6451 | 253822 | 207919 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6BJ | SA146BJ | sa14 6bj | sa146bj | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1607 | Over1500 | 3.2165 | 2.3535 | 1.7259 | 29.952 | 15.9744 | 17.6559 | 253788 | 208151 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6BL | SA146BL | sa14 6bl | sa146bl | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1607 | Over1500 | 3.2165 | 2.3535 | 1.7259 | 29.952 | 15.9744 | 17.6559 | 253827 | 208033 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6BQ | SA146BQ | sa14 6bq | sa146bq | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1607 | Over1500 | 3.2165 | 2.3535 | 1.7259 | 29.952 | 15.9744 | 17.6559 | 254003 | 208218 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6BU | SA146BU | sa14 6bu | sa146bu | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1612 | Over1500 | 3.2265 | 2.3608 | 1.7313 | 30.0451 | 16.0241 | 17.7108 | 254665 | 210167 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6DQ | SA146DQ | sa14 6dq | sa146dq | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 255778 | 213361 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6DT | SA146DT | sa14 6dt | sa146dt | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1607 | Over1500 | 3.2165 | 2.3535 | 1.7259 | 29.952 | 15.9744 | 17.6559 | 254688 | 211702 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6DY | SA146DY | sa14 6dy | sa146dy | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1559 | Over1500 | 3.1204 | 2.2832 | 1.6744 | 29.0573 | 15.4972 | 17.1285 | 254880 | 212058 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6DZ | SA146DZ | sa14 6dz | sa146dz | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1539 | Over1500 | 3.0804 | 2.2539 | 1.6529 | 28.6845 | 15.2984 | 16.9088 | 257613 | 210735 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6ED | SA146ED | sa14 6ed | sa146ed | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1617 | Over1500 | 3.2365 | 2.3682 | 1.7367 | 30.1383 | 16.0738 | 17.7658 | 255038 | 212045 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6EF | SA146EF | sa14 6ef | sa146ef | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257378 | 212870 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6EG | SA146EG | sa14 6eg | sa146eg | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257052 | 212813 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6EH | SA146EH | sa14 6eh | sa146eh | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256098 | 213189 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6EJ | SA146EJ | sa14 6ej | sa146ej | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256128 | 213270 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6EX | SA146EX | sa14 6ex | sa146ex | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256178 | 212541 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6LR | SA146LR | sa14 6lr | sa146lr | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256052 | 212576 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6LT | SA146LT | sa14 6lt | sa146lt | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256030 | 212432 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6LU | SA146LU | sa14 6lu | sa146lu | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1617 | Over1500 | 3.2365 | 2.3682 | 1.7367 | 30.1383 | 16.0738 | 17.7658 | 255665 | 212374 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6LY | SA146LY | sa14 6ly | sa146ly | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1617 | Over1500 | 3.2365 | 2.3682 | 1.7367 | 30.1383 | 16.0738 | 17.7658 | 255394 | 212252 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6NA | SA146NA | sa14 6na | sa146na | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256236 | 212780 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6NB | SA146NB | sa14 6nb | sa146nb | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256167 | 212930 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6ND | SA146ND | sa14 6nd | sa146nd | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256268 | 212860 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6NE | SA146NE | sa14 6ne | sa146ne | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256439 | 212608 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6NF | SA146NF | sa14 6nf | sa146nf | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256409 | 212732 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6NG | SA146NG | sa14 6ng | sa146ng | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256431 | 212703 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6NH | SA146NH | sa14 6nh | sa146nh | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256305 | 212717 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6NJ | SA146NJ | sa14 6nj | sa146nj | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256359 | 212537 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6NL | SA146NL | sa14 6nl | sa146nl | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256326 | 212613 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6NN | SA146NN | sa14 6nn | sa146nn | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256301 | 212785 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6NS | SA146NS | sa14 6ns | sa146ns | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256125 | 212573 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6NT | SA146NT | sa14 6nt | sa146nt | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256232 | 212557 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6PA | SA146PA | sa14 6pa | sa146pa | Carmarthenshire | Sir Gaerfyrddin | Cwmtawel |  | 1576 | Over1500 | 3.1544 | 2.3081 | 1.6926 | 29.3742 | 15.6662 | 17.3153 | 256661 | 211618 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6PB | SA146PB | sa14 6pb | sa146pb | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1576 | Over1500 | 3.1544 | 2.3081 | 1.6926 | 29.3742 | 15.6662 | 17.3153 | 256767 | 211698 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6PD | SA146PD | sa14 6pd | sa146pd | Carmarthenshire | Sir Gaerfyrddin | Cwmtawel |  | 1576 | Over1500 | 3.1544 | 2.3081 | 1.6926 | 29.3742 | 15.6662 | 17.3153 | 256780 | 211426 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6PG | SA146PG | sa14 6pg | sa146pg | Carmarthenshire | Sir Gaerfyrddin | Cwmtawel |  | 1576 | Over1500 | 3.1544 | 2.3081 | 1.6926 | 29.3742 | 15.6662 | 17.3153 | 256973 | 211012 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6PH | SA146PH | sa14 6ph | sa146ph | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1539 | Over1500 | 3.0804 | 2.2539 | 1.6529 | 28.6845 | 15.2984 | 16.9088 | 257187 | 210511 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6PP | SA146PP | sa14 6pp | sa146pp | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1539 | Over1500 | 3.0804 | 2.2539 | 1.6529 | 28.6845 | 15.2984 | 16.9088 | 257280 | 210352 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6PR | SA146PR | sa14 6pr | sa146pr | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1539 | Over1500 | 3.0804 | 2.2539 | 1.6529 | 28.6845 | 15.2984 | 16.9088 | 257497 | 210727 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6PS | SA146PS | sa14 6ps | sa146ps | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1539 | Over1500 | 3.0804 | 2.2539 | 1.6529 | 28.6845 | 15.2984 | 16.9088 | 257598 | 210824 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6PT | SA146PT | sa14 6pt | sa146pt | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1565 | Over1500 | 3.1324 | 2.292 | 1.6808 | 29.1691 | 15.5569 | 17.1944 | 257694 | 211206 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6PT | SA146PT | sa14 6pt | sa146pt | Carmarthenshire | Sir Gaerfyrddin | Cwmtawel |  | 1565 | Over1500 | 3.1324 | 2.292 | 1.6808 | 29.1691 | 15.5569 | 17.1944 | 257694 | 211206 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6PU | SA146PU | sa14 6pu | sa146pu | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1565 | Over1500 | 3.1324 | 2.292 | 1.6808 | 29.1691 | 15.5569 | 17.1944 | 257737 | 211035 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6PX | SA146PX | sa14 6px | sa146px | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1539 | Over1500 | 3.0804 | 2.2539 | 1.6529 | 28.6845 | 15.2984 | 16.9088 | 257694 | 210812 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RA | SA146RA | sa14 6ra | sa146ra | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1565 | Over1500 | 3.1324 | 2.292 | 1.6808 | 29.1691 | 15.5569 | 17.1944 | 257103 | 211945 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RA | SA146RA | sa14 6ra | sa146ra | Carmarthenshire | Sir Gaerfyrddin | Cwmtawel |  | 1565 | Over1500 | 3.1324 | 2.292 | 1.6808 | 29.1691 | 15.5569 | 17.1944 | 257103 | 211945 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RB | SA146RB | sa14 6rb | sa146rb | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256889 | 212607 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RD | SA146RD | sa14 6rd | sa146rd | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256410 | 213044 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RE | SA146RE | sa14 6re | sa146re | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 257003 | 212718 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RE | SA146RE | sa14 6re | sa146re | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 257003 | 212718 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RF | SA146RF | sa14 6rf | sa146rf | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256731 | 212289 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RG | SA146RG | sa14 6rg | sa146rg | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256453 | 213161 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RH | SA146RH | sa14 6rh | sa146rh | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256611 | 213214 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RJ | SA146RJ | sa14 6rj | sa146rj | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256601 | 212633 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RL | SA146RL | sa14 6rl | sa146rl | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256769 | 213054 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RN | SA146RN | sa14 6rn | sa146rn | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256549 | 213286 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RP | SA146RP | sa14 6rp | sa146rp | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256755 | 213390 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RR | SA146RR | sa14 6rr | sa146rr | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256908 | 213559 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RT | SA146RT | sa14 6rt | sa146rt | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1656 | Over1500 | 3.3145 | 2.4253 | 1.7785 | 30.8652 | 16.4615 | 18.1942 | 257145 | 213352 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RU | SA146RU | sa14 6ru | sa146ru | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1656 | Over1500 | 3.3145 | 2.4253 | 1.7785 | 30.8652 | 16.4615 | 18.1942 | 257338 | 213118 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RW | SA146RW | sa14 6rw | sa146rw | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256662 | 213271 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RX | SA146RX | sa14 6rx | sa146rx | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257191 | 212643 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RX | SA146RX | sa14 6rx | sa146rx | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257191 | 212643 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RY | SA146RY | sa14 6ry | sa146ry | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257374 | 212681 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6RZ | SA146RZ | sa14 6rz | sa146rz | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256574 | 212231 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SA | SA146SA | sa14 6sa | sa146sa | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257568 | 212971 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SB | SA146SB | sa14 6sb | sa146sb | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257911 | 212675 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SD | SA146SD | sa14 6sd | sa146sd | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258088 | 212530 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SE | SA146SE | sa14 6se | sa146se | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257919 | 212333 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SF | SA146SF | sa14 6sf | sa146sf | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1565 | Over1500 | 3.1324 | 2.292 | 1.6808 | 29.1691 | 15.5569 | 17.1944 | 257606 | 211831 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SF | SA146SF | sa14 6sf | sa146sf | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1565 | Over1500 | 3.1324 | 2.292 | 1.6808 | 29.1691 | 15.5569 | 17.1944 | 257606 | 211831 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SG | SA146SG | sa14 6sg | sa146sg | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256726 | 213142 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SH | SA146SH | sa14 6sh | sa146sh | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256728 | 213432 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SJ | SA146SJ | sa14 6sj | sa146sj | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257705 | 212749 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SL | SA146SL | sa14 6sl | sa146sl | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257812 | 212702 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SN | SA146SN | sa14 6sn | sa146sn | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257642 | 212740 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SP | SA146SP | sa14 6sp | sa146sp | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256080 | 212782 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SQ | SA146SQ | sa14 6sq | sa146sq | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257626 | 212810 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SR | SA146SR | sa14 6sr | sa146sr | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 256041 | 212774 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SS | SA146SS | sa14 6ss | sa146ss | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257806 | 212779 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6ST | SA146ST | sa14 6st | sa146st | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256100 | 213021 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SU | SA146SU | sa14 6su | sa146su | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 255911 | 213202 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SW | SA146SW | sa14 6sw | sa146sw | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257694 | 212809 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SX | SA146SX | sa14 6sx | sa146sx | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1576 | Over1500 | 3.1544 | 2.3081 | 1.6926 | 29.3742 | 15.6662 | 17.3153 | 256864 | 211967 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SY | SA146SY | sa14 6sy | sa146sy | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1623 | Over1500 | 3.2485 | 2.3769 | 1.7431 | 30.2502 | 16.1334 | 17.8317 | 256220 | 213080 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6SZ | SA146SZ | sa14 6sz | sa146sz | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 255879 | 213090 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6TA | SA146TA | sa14 6ta | sa146ta | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 255648 | 213260 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 6TD | SA146TD | sa14 6td | sa146td | Carmarthenshire | Sir Gaerfyrddin | Cross Hands |  | 1589 | Over1500 | 3.1804 | 2.3272 | 1.7066 | 29.6165 | 15.7954 | 17.4581 | 255553 | 213369 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7DX | SA147DX | sa14 7dx | sa147dx | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258763 | 212811 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7DY | SA147DY | sa14 7dy | sa147dy | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258767 | 212557 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7LU | SA147LU | sa14 7lu | sa147lu | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 257954 | 214869 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7LX | SA147LX | sa14 7lx | sa147lx | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 257814 | 214737 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7LY | SA147LY | sa14 7ly | sa147ly | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 257894 | 214868 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7NA | SA147NA | sa14 7na | sa147na | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1785 | Over1500 | 3.5727 | 2.6142 | 1.9171 | 33.2696 | 17.7438 | 19.6116 | 257872 | 215006 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7ND | SA147ND | sa14 7nd | sa147nd | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258912 | 212333 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7NP | SA147NP | sa14 7np | sa147np | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258615 | 213482 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7NS | SA147NS | sa14 7ns | sa147ns | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258641 | 213354 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7NT | SA147NT | sa14 7nt | sa147nt | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258773 | 213346 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7NU | SA147NU | sa14 7nu | sa147nu | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258393 | 213244 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7NU | SA147NU | sa14 7nu | sa147nu | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258393 | 213244 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7NW | SA147NW | sa14 7nw | sa147nw | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257804 | 212805 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PB | SA147PB | sa14 7pb | sa147pb | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258035 | 213124 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PE | SA147PE | sa14 7pe | sa147pe | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1618 | Over1500 | 3.2385 | 2.3696 | 1.7377 | 30.157 | 16.0837 | 17.7767 | 257853 | 212967 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PF | SA147PF | sa14 7pf | sa147pf | Carmarthenshire | Sir Gaerfyrddin | Cwmgwili |  | 1656 | Over1500 | 3.3145 | 2.4253 | 1.7785 | 30.8652 | 16.4615 | 18.1942 | 257963 | 213045 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PG | SA147PG | sa14 7pg | sa147pg | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258577 | 213287 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PH | SA147PH | sa14 7ph | sa147ph | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258827 | 213371 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PJ | SA147PJ | sa14 7pj | sa147pj | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258892 | 213308 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PN | SA147PN | sa14 7pn | sa147pn | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258735 | 213153 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PR | SA147PR | sa14 7pr | sa147pr | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258862 | 213127 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PS | SA147PS | sa14 7ps | sa147ps | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258854 | 212913 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PT | SA147PT | sa14 7pt | sa147pt | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258897 | 212841 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PU | SA147PU | sa14 7pu | sa147pu | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258793 | 212761 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PW | SA147PW | sa14 7pw | sa147pw | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258818 | 213245 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PY | SA147PY | sa14 7py | sa147py | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258939 | 212636 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7PZ | SA147PZ | sa14 7pz | sa147pz | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1596 | Over1500 | 3.1945 | 2.3374 | 1.7141 | 29.7469 | 15.865 | 17.535 | 259073 | 212665 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RB | SA147RB | sa14 7rb | sa147rb | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258814 | 212402 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RD | SA147RD | sa14 7rd | sa147rd | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258935 | 212256 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RE | SA147RE | sa14 7re | sa147re | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1596 | Over1500 | 3.1945 | 2.3374 | 1.7141 | 29.7469 | 15.865 | 17.535 | 259054 | 212634 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RF | SA147RF | sa14 7rf | sa147rf | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258744 | 212618 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RG | SA147RG | sa14 7rg | sa147rg | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258735 | 212425 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RH | SA147RH | sa14 7rh | sa147rh | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258939 | 212571 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RJ | SA147RJ | sa14 7rj | sa147rj | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258643 | 212552 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RL | SA147RL | sa14 7rl | sa147rl | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258410 | 213806 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RN | SA147RN | sa14 7rn | sa147rn | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1652 | Over1500 | 3.3065 | 2.4194 | 1.7742 | 30.7907 | 16.4217 | 18.1503 | 258152 | 214059 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RP | SA147RP | sa14 7rp | sa147rp | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258526 | 213631 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RQ | SA147RQ | sa14 7rq | sa147rq | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1652 | Over1500 | 3.3065 | 2.4194 | 1.7742 | 30.7907 | 16.4217 | 18.1503 | 258159 | 214129 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RS | SA147RS | sa14 7rs | sa147rs | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258371 | 213650 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RT | SA147RT | sa14 7rt | sa147rt | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258255 | 213652 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RU | SA147RU | sa14 7ru | sa147ru | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1656 | Over1500 | 3.3145 | 2.4253 | 1.7785 | 30.8652 | 16.4615 | 18.1942 | 257986 | 213573 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RW | SA147RW | sa14 7rw | sa147rw | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 257865 | 214521 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RX | SA147RX | sa14 7rx | sa147rx | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258417 | 213592 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RY | SA147RY | sa14 7ry | sa147ry | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258566 | 213690 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7RZ | SA147RZ | sa14 7rz | sa147rz | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1670 | Over1500 | 3.3426 | 2.4458 | 1.7936 | 31.1262 | 16.6006 | 18.3481 | 258135 | 213571 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7SA | SA147SA | sa14 7sa | sa147sa | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1770 | Over1500 | 3.5427 | 2.5922 | 1.901 | 32.99 | 17.5947 | 19.4467 | 258953 | 215377 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7SD | SA147SD | sa14 7sd | sa147sd | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1770 | Over1500 | 3.5427 | 2.5922 | 1.901 | 32.99 | 17.5947 | 19.4467 | 258719 | 215198 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7SE | SA147SE | sa14 7se | sa147se | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1770 | Over1500 | 3.5427 | 2.5922 | 1.901 | 32.99 | 17.5947 | 19.4467 | 258836 | 215399 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7SG | SA147SG | sa14 7sg | sa147sg | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1732 | Over1500 | 3.4667 | 2.5366 | 1.8602 | 32.2818 | 17.2169 | 19.0292 | 258242 | 216489 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7SH | SA147SH | sa14 7sh | sa147sh | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1762 | Over1500 | 3.5267 | 2.5805 | 1.8924 | 32.8409 | 17.5152 | 19.3589 | 257947 | 216439 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7TG | SA147TG | sa14 7tg | sa147tg | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1732 | Over1500 | 3.4667 | 2.5366 | 1.8602 | 32.2818 | 17.2169 | 19.0292 | 258729 | 216558 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7TH | SA147TH | sa14 7th | sa147th | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1732 | Over1500 | 3.4667 | 2.5366 | 1.8602 | 32.2818 | 17.2169 | 19.0292 | 258789 | 216610 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7TL | SA147TL | sa14 7tl | sa147tl | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1732 | Over1500 | 3.4667 | 2.5366 | 1.8602 | 32.2818 | 17.2169 | 19.0292 | 258776 | 216445 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7TN | SA147TN | sa14 7tn | sa147tn | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1732 | Over1500 | 3.4667 | 2.5366 | 1.8602 | 32.2818 | 17.2169 | 19.0292 | 258728 | 216488 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7TP | SA147TP | sa14 7tp | sa147tp | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1722 | Over1500 | 3.4466 | 2.5219 | 1.8494 | 32.0954 | 17.1175 | 18.9194 | 259177 | 216463 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7TW | SA147TW | sa14 7tw | sa147tw | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1732 | Over1500 | 3.4667 | 2.5366 | 1.8602 | 32.2818 | 17.2169 | 19.0292 | 258735 | 216420 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7UA | SA147UA | sa14 7ua | sa147ua | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1732 | Over1500 | 3.4667 | 2.5366 | 1.8602 | 32.2818 | 17.2169 | 19.0292 | 258674 | 216675 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7UD | SA147UD | sa14 7ud | sa147ud | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1645 | Over1500 | 3.2925 | 2.4092 | 1.7667 | 30.6602 | 16.3521 | 18.0734 | 258775 | 217060 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7UE | SA147UE | sa14 7ue | sa147ue | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1609 | Over1500 | 3.2205 | 2.3564 | 1.7281 | 29.9892 | 15.9943 | 17.6779 | 259189 | 217038 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7UF | SA147UF | sa14 7uf | sa147uf | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1645 | Over1500 | 3.2925 | 2.4092 | 1.7667 | 30.6602 | 16.3521 | 18.0734 | 258929 | 217379 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7UG | SA147UG | sa14 7ug | sa147ug | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1645 | Over1500 | 3.2925 | 2.4092 | 1.7667 | 30.6602 | 16.3521 | 18.0734 | 258962 | 217505 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 7UL | SA147UL | sa14 7ul | sa147ul | Carmarthenshire | Sir Gaerfyrddin | Carmel & Pant-Y-Llyn |  | 1732 | Over1500 | 3.4667 | 2.5366 | 1.8602 | 32.2818 | 17.2169 | 19.0292 | 258636 | 216600 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8AH | SA148AH | sa14 8ah | sa148ah | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1284 | 1200-1500 | 2.57 | 1.8805 | 1.379 | 23.9317 | 12.7636 | 14.1071 | 256006 | 200886 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8AJ | SA148AJ | sa14 8aj | sa148aj | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1338 | 1200-1500 | 2.6781 | 1.9596 | 1.437 | 24.9382 | 13.3004 | 14.7004 | 255568 | 202547 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8AQ | SA148AQ | sa14 8aq | sa148aq | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1338 | 1200-1500 | 2.6781 | 1.9596 | 1.437 | 24.9382 | 13.3004 | 14.7004 | 255686 | 202465 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8AX | SA148AX | sa14 8ax | sa148ax | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1338 | 1200-1500 | 2.6781 | 1.9596 | 1.437 | 24.9382 | 13.3004 | 14.7004 | 255448 | 202789 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8BA | SA148BA | sa14 8ba | sa148ba | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1338 | 1200-1500 | 2.6781 | 1.9596 | 1.437 | 24.9382 | 13.3004 | 14.7004 | 255790 | 202394 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8DJ | SA148DJ | sa14 8dj | sa148dj | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255655 | 201777 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8DQ | SA148DQ | sa14 8dq | sa148dq | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1290 | 1200-1500 | 2.582 | 1.8893 | 1.3855 | 24.0436 | 12.8232 | 14.1731 | 254272 | 200979 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8DZ | SA148DZ | sa14 8dz | sa148dz | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1338 | 1200-1500 | 2.6781 | 1.9596 | 1.437 | 24.9382 | 13.3004 | 14.7004 | 255860 | 202266 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8EF | SA148EF | sa14 8ef | sa148ef | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255931 | 201782 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8GA | SA148GA | sa14 8ga | sa148ga | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1284 | 1200-1500 | 2.57 | 1.8805 | 1.379 | 23.9317 | 12.7636 | 14.1071 | 255622 | 200959 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8GB | SA148GB | sa14 8gb | sa148gb | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1284 | 1200-1500 | 2.57 | 1.8805 | 1.379 | 23.9317 | 12.7636 | 14.1071 | 255714 | 200918 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8GD | SA148GD | sa14 8gd | sa148gd | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255738 | 201068 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8GE | SA148GE | sa14 8ge | sa148ge | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255693 | 201063 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8GF | SA148GF | sa14 8gf | sa148gf | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255687 | 200991 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8JH | SA148JH | sa14 8jh | sa148jh | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1515 | Over1500 | 3.0323 | 2.2188 | 1.6271 | 28.2372 | 15.0599 | 16.6451 | 253778 | 207258 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8JJ | SA148JJ | sa14 8jj | sa148jj | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 254444 | 208228 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8JT | SA148JT | sa14 8jt | sa148jt | Carmarthenshire | Sir Gaerfyrddin | Llannon |  | 1549 | Over1500 | 3.1004 | 2.2686 | 1.6636 | 28.8709 | 15.3978 | 17.0187 | 254735 | 207205 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8QH | SA148QH | sa14 8qh | sa148qh | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254471 | 200772 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8QJ | SA148QJ | sa14 8qj | sa148qj | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254618 | 200739 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8QL | SA148QL | sa14 8ql | sa148ql | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254805 | 200848 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8QP | SA148QP | sa14 8qp | sa148qp | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1338 | 1200-1500 | 2.6781 | 1.9596 | 1.437 | 24.9382 | 13.3004 | 14.7004 | 256007 | 202030 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8QQ | SA148QQ | sa14 8qq | sa148qq | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254504 | 200690 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8QS | SA148QS | sa14 8qs | sa148qs | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255480 | 201228 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8RX | SA148RX | sa14 8rx | sa148rx | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 256006 | 201183 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8SJ | SA148SJ | sa14 8sj | sa148sj | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255806 | 201120 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8SX | SA148SX | sa14 8sx | sa148sx | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255946 | 201135 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8SZ | SA148SZ | sa14 8sz | sa148sz | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255864 | 201184 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TE | SA148TE | sa14 8te | sa148te | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255556 | 201113 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TF | SA148TF | sa14 8tf | sa148tf | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255661 | 201198 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TG | SA148TG | sa14 8tg | sa148tg | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255726 | 201189 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TH | SA148TH | sa14 8th | sa148th | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255860 | 201303 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TJ | SA148TJ | sa14 8tj | sa148tj | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255953 | 201243 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TL | SA148TL | sa14 8tl | sa148tl | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256053 | 201480 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TN | SA148TN | sa14 8tn | sa148tn | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256060 | 201608 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TP | SA148TP | sa14 8tp | sa148tp | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255950 | 201655 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TQ | SA148TQ | sa14 8tq | sa148tq | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255994 | 201293 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TR | SA148TR | sa14 8tr | sa148tr | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255910 | 201678 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TS | SA148TS | sa14 8ts | sa148ts | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256160 | 201804 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TT | SA148TT | sa14 8tt | sa148tt | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256186 | 201877 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TU | SA148TU | sa14 8tu | sa148tu | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256066 | 201943 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TW | SA148TW | sa14 8tw | sa148tw | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256037 | 201641 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TX | SA148TX | sa14 8tx | sa148tx | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255931 | 201310 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TY | SA148TY | sa14 8ty | sa148ty | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1338 | 1200-1500 | 2.6781 | 1.9596 | 1.437 | 24.9382 | 13.3004 | 14.7004 | 255950 | 202037 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8TZ | SA148TZ | sa14 8tz | sa148tz | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255927 | 201221 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UA | SA148UA | sa14 8ua | sa148ua | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255907 | 201875 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UB | SA148UB | sa14 8ub | sa148ub | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256045 | 201835 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UD | SA148UD | sa14 8ud | sa148ud | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256230 | 201562 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UE | SA148UE | sa14 8ue | sa148ue | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256208 | 201550 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UF | SA148UF | sa14 8uf | sa148uf | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256128 | 201457 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UG | SA148UG | sa14 8ug | sa148ug | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256285 | 201664 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UH | SA148UH | sa14 8uh | sa148uh | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256306 | 201688 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UJ | SA148UJ | sa14 8uj | sa148uj | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256022 | 201399 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UL | SA148UL | sa14 8ul | sa148ul | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256234 | 201887 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UN | SA148UN | sa14 8un | sa148un | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1326 | 1200-1500 | 2.654 | 1.942 | 1.4241 | 24.7146 | 13.1811 | 14.5686 | 256631 | 202365 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UP | SA148UP | sa14 8up | sa148up | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255375 | 201265 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UQ | SA148UQ | sa14 8uq | sa148uq | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255562 | 201204 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UR | SA148UR | sa14 8ur | sa148ur | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255481 | 201356 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8US | SA148US | sa14 8us | sa148us | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256347 | 201828 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UU | SA148UU | sa14 8uu | sa148uu | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256115 | 201340 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UW | SA148UW | sa14 8uw | sa148uw | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1326 | 1200-1500 | 2.654 | 1.942 | 1.4241 | 24.7146 | 13.1811 | 14.5686 | 256624 | 202454 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UX | SA148UX | sa14 8ux | sa148ux | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256347 | 201426 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UY | SA148UY | sa14 8uy | sa148uy | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256365 | 201269 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8UZ | SA148UZ | sa14 8uz | sa148uz | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 256371 | 201498 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8WA | SA148WA | sa14 8wa | sa148wa | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255451 | 201302 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8WB | SA148WB | sa14 8wb | sa148wb | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255566 | 201152 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8WD | SA148WD | sa14 8wd | sa148wd | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255683 | 201318 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8WF | SA148WF | sa14 8wf | sa148wf | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255503 | 201137 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8XP | SA148XP | sa14 8xp | sa148xp | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1326 | 1200-1500 | 2.654 | 1.942 | 1.4241 | 24.7146 | 13.1811 | 14.5686 | 256205 | 202323 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8XT | SA148XT | sa14 8xt | sa148xt | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1326 | 1200-1500 | 2.654 | 1.942 | 1.4241 | 24.7146 | 13.1811 | 14.5686 | 256349 | 202119 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8XW | SA148XW | sa14 8xw | sa148xw | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1326 | 1200-1500 | 2.654 | 1.942 | 1.4241 | 24.7146 | 13.1811 | 14.5686 | 256306 | 202361 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8XY | SA148XY | sa14 8xy | sa148xy | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1326 | 1200-1500 | 2.654 | 1.942 | 1.4241 | 24.7146 | 13.1811 | 14.5686 | 256268 | 202133 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8XZ | SA148XZ | sa14 8xz | sa148xz | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1326 | 1200-1500 | 2.654 | 1.942 | 1.4241 | 24.7146 | 13.1811 | 14.5686 | 256379 | 202246 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YA | SA148YA | sa14 8ya | sa148ya | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1326 | 1200-1500 | 2.654 | 1.942 | 1.4241 | 24.7146 | 13.1811 | 14.5686 | 256127 | 202276 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YB | SA148YB | sa14 8yb | sa148yb | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1326 | 1200-1500 | 2.654 | 1.942 | 1.4241 | 24.7146 | 13.1811 | 14.5686 | 256462 | 202414 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YE | SA148YE | sa14 8ye | sa148ye | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1326 | 1200-1500 | 2.654 | 1.942 | 1.4241 | 24.7146 | 13.1811 | 14.5686 | 256613 | 202280 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YF | SA148YF | sa14 8yf | sa148yf | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1326 | 1200-1500 | 2.654 | 1.942 | 1.4241 | 24.7146 | 13.1811 | 14.5686 | 256832 | 202518 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YH | SA148YH | sa14 8yh | sa148yh | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1311 | 1200-1500 | 2.624 | 1.92 | 1.408 | 24.435 | 13.032 | 14.4038 | 257048 | 202731 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YJ | SA148YJ | sa14 8yj | sa148yj | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1326 | 1200-1500 | 2.654 | 1.942 | 1.4241 | 24.7146 | 13.1811 | 14.5686 | 256176 | 202384 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YL | SA148YL | sa14 8yl | sa148yl | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1311 | 1200-1500 | 2.624 | 1.92 | 1.408 | 24.435 | 13.032 | 14.4038 | 257102 | 202781 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YP | SA148YP | sa14 8yp | sa148yp | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1338 | 1200-1500 | 2.6781 | 1.9596 | 1.437 | 24.9382 | 13.3004 | 14.7004 | 255769 | 201993 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YR | SA148YR | sa14 8yr | sa148yr | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255517 | 201802 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YS | SA148YS | sa14 8ys | sa148ys | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1338 | 1200-1500 | 2.6781 | 1.9596 | 1.437 | 24.9382 | 13.3004 | 14.7004 | 255425 | 202067 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YT | SA148YT | sa14 8yt | sa148yt | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1338 | 1200-1500 | 2.6781 | 1.9596 | 1.437 | 24.9382 | 13.3004 | 14.7004 | 255672 | 202308 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YU | SA148YU | sa14 8yu | sa148yu | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1338 | 1200-1500 | 2.6781 | 1.9596 | 1.437 | 24.9382 | 13.3004 | 14.7004 | 255408 | 202328 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 8YW | SA148YW | sa14 8yw | sa148yw | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255711 | 201896 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9RP | SA149RP | sa14 9rp | sa149rp | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254547 | 200546 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9RQ | SA149RQ | sa14 9rq | sa149rq | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254862 | 200906 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9RR | SA149RR | sa14 9rr | sa149rr | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254971 | 200861 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9RT | SA149RT | sa14 9rt | sa149rt | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1284 | 1200-1500 | 2.57 | 1.8805 | 1.379 | 23.9317 | 12.7636 | 14.1071 | 255689 | 200763 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9RW | SA149RW | sa14 9rw | sa149rw | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254348 | 200438 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9RY | SA149RY | sa14 9ry | sa149ry | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1274 | 1200-1500 | 2.55 | 1.8658 | 1.3683 | 23.7454 | 12.6642 | 13.9973 | 255769 | 201167 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9TT | SA149TT | sa14 9tt | sa149tt | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254259 | 200678 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9TU | SA149TU | sa14 9tu | sa149tu | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254357 | 200556 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9TY | SA149TY | sa14 9ty | sa149ty | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254393 | 200642 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UA | SA149UA | sa14 9ua | sa149ua | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254541 | 200693 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UB | SA149UB | sa14 9ub | sa149ub | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254675 | 200553 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UD | SA149UD | sa14 9ud | sa149ud | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254700 | 200635 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UE | SA149UE | sa14 9ue | sa149ue | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254854 | 200637 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UF | SA149UF | sa14 9uf | sa149uf | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254805 | 200730 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UG | SA149UG | sa14 9ug | sa149ug | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254933 | 200680 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UH | SA149UH | sa14 9uh | sa149uh | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254994 | 200780 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UJ | SA149UJ | sa14 9uj | sa149uj | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254826 | 200519 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UL | SA149UL | sa14 9ul | sa149ul | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1284 | 1200-1500 | 2.57 | 1.8805 | 1.379 | 23.9317 | 12.7636 | 14.1071 | 255093 | 200774 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UN | SA149UN | sa14 9un | sa149un | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1284 | 1200-1500 | 2.57 | 1.8805 | 1.379 | 23.9317 | 12.7636 | 14.1071 | 255175 | 200853 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UP | SA149UP | sa14 9up | sa149up | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1284 | 1200-1500 | 2.57 | 1.8805 | 1.379 | 23.9317 | 12.7636 | 14.1071 | 255468 | 200960 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UQ | SA149UQ | sa14 9uq | sa149uq | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254798 | 200415 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UR | SA149UR | sa14 9ur | sa149ur | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1288 | 1200-1500 | 2.578 | 1.8863 | 1.3833 | 24.0063 | 12.8034 | 14.1511 | 254773 | 200770 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA14 9UW | SA149UW | sa14 9uw | sa149uw | Carmarthenshire | Sir Gaerfyrddin | Llangennech |  | 1284 | 1200-1500 | 2.57 | 1.8805 | 1.379 | 23.9317 | 12.7636 | 14.1071 | 255498 | 200887 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AB | SA181AB | sa18 1ab | sa181ab | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271373 | 214436 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AD | SA181AD | sa18 1ad | sa181ad | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271398 | 214382 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AE | SA181AE | sa18 1ae | sa181ae | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271512 | 214502 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AF | SA181AF | sa18 1af | sa181af | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271532 | 214383 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AG | SA181AG | sa18 1ag | sa181ag | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271694 | 214376 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AH | SA181AH | sa18 1ah | sa181ah | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271706 | 214484 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AJ | SA181AJ | sa18 1aj | sa181aj | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1603 | Over1500 | 3.2085 | 2.3477 | 1.7216 | 29.8774 | 15.9346 | 17.6119 | 269170 | 213201 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AL | SA181AL | sa18 1al | sa181al | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271606 | 214470 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AN | SA181AN | sa18 1an | sa181an | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271791 | 214883 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AP | SA181AP | sa18 1ap | sa181ap | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271575 | 214714 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AR | SA181AR | sa18 1ar | sa181ar | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271453 | 214863 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AS | SA181AS | sa18 1as | sa181as | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271619 | 214805 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AT | SA181AT | sa18 1at | sa181at | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271312 | 214342 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AU | SA181AU | sa18 1au | sa181au | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271266 | 214462 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AW | SA181AW | sa18 1aw | sa181aw | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271662 | 214794 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1AX | SA181AX | sa18 1ax | sa181ax | Neath Port Talbot | Castell-nedd Port Talbot | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270486 | 211078 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1AZ | SA181AZ | sa18 1az | sa181az | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268452 | 213324 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BA | SA181BA | sa18 1ba | sa181ba | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271163 | 214330 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BB | SA181BB | sa18 1bb | sa181bb | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271080 | 214424 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BD | SA181BD | sa18 1bd | sa181bd | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271042 | 214187 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BE | SA181BE | sa18 1be | sa181be | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1711 | Over1500 | 3.4246 | 2.5058 | 1.8376 | 31.8904 | 17.0082 | 18.7985 | 270857 | 214305 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BG | SA181BG | sa18 1bg | sa181bg | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1711 | Over1500 | 3.4246 | 2.5058 | 1.8376 | 31.8904 | 17.0082 | 18.7985 | 270864 | 214263 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BH | SA181BH | sa18 1bh | sa181bh | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1711 | Over1500 | 3.4246 | 2.5058 | 1.8376 | 31.8904 | 17.0082 | 18.7985 | 270767 | 213988 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BJ | SA181BJ | sa18 1bj | sa181bj | Neath Port Talbot | Castell-nedd Port Talbot | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270773 | 213786 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1BL | SA181BL | sa18 1bl | sa181bl | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1711 | Over1500 | 3.4246 | 2.5058 | 1.8376 | 31.8904 | 17.0082 | 18.7985 | 270667 | 214221 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BN | SA181BN | sa18 1bn | sa181bn | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1711 | Over1500 | 3.4246 | 2.5058 | 1.8376 | 31.8904 | 17.0082 | 18.7985 | 270624 | 214308 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BR | SA181BR | sa18 1br | sa181br | Neath Port Talbot | Castell-nedd Port Talbot | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270047 | 212617 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1BS | SA181BS | sa18 1bs | sa181bs | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268724 | 213091 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BT | SA181BT | sa18 1bt | sa181bt | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271374 | 214277 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BU | SA181BU | sa18 1bu | sa181bu | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271583 | 214305 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BW | SA181BW | sa18 1bw | sa181bw | Carmarthenshire | Sir Gaerfyrddin | Nantgwineu |  | 1711 | Over1500 | 3.4246 | 2.5058 | 1.8376 | 31.8904 | 17.0082 | 18.7985 | 270230 | 214111 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BX | SA181BX | sa18 1bx | sa181bx | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268033 | 213363 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BY | SA181BY | sa18 1by | sa181by | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271617 | 214276 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1BZ | SA181BZ | sa18 1bz | sa181bz | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268055 | 213415 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1DA | SA181DA | sa18 1da | sa181da | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271914 | 214285 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1DB | SA181DB | sa18 1db | sa181db | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1724 | Over1500 | 3.4507 | 2.5249 | 1.8516 | 32.1327 | 17.1374 | 18.9414 | 272251 | 214236 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1DE | SA181DE | sa18 1de | sa181de | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1724 | Over1500 | 3.4507 | 2.5249 | 1.8516 | 32.1327 | 17.1374 | 18.9414 | 272469 | 214458 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1DF | SA181DF | sa18 1df | sa181df | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1724 | Over1500 | 3.4507 | 2.5249 | 1.8516 | 32.1327 | 17.1374 | 18.9414 | 272196 | 214722 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1DG | SA181DG | sa18 1dg | sa181dg | Carmarthenshire | Sir Gaerfyrddin | Garnswllt |  | 1724 | Over1500 | 3.4507 | 2.5249 | 1.8516 | 32.1327 | 17.1374 | 18.9414 | 272595 | 214203 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1DH | SA181DH | sa18 1dh | sa181dh | BBNPA |  | Garnswllt |  | 1768 | Over1500 | 3.5387 | 2.5893 | 1.8988 | 32.9527 | 17.5748 | 19.4248 | 273104 | 214004 | Brecon Beacons National Park LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA18 1DJ | SA181DJ | sa18 1dj | sa181dj | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267673 | 213590 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1DL | SA181DL | sa18 1dl | sa181dl | BBNPA |  | Garnswllt |  | 1768 | Over1500 | 3.5387 | 2.5893 | 1.8988 | 32.9527 | 17.5748 | 19.4248 | 273398 | 214093 | Brecon Beacons National Park LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA18 1DN | SA181DN | sa18 1dn | sa181dn | BBNPA |  | Garnswllt |  | 1751 | Over1500 | 3.5047 | 2.5644 | 1.8806 | 32.6359 | 17.4058 | 19.238 | 273319 | 213971 | Brecon Beacons National Park LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA18 1DP | SA181DP | sa18 1dp | sa181dp | BBNPA |  | Garnswllt |  | 1751 | Over1500 | 3.5047 | 2.5644 | 1.8806 | 32.6359 | 17.4058 | 19.238 | 273648 | 213924 | Brecon Beacons National Park LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA18 1DQ | SA181DQ | sa18 1dq | sa181dq | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268086 | 213506 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1DT | SA181DT | sa18 1dt | sa181dt | Carmarthenshire |  | Garnswllt |  | 1749 | Over1500 | 3.5007 | 2.5615 | 1.8784 | 32.5986 | 17.3859 | 19.216 | 269997 | 211945 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1DW | SA181DW | sa18 1dw | sa181dw | Carmarthenshire |  | Garnswllt |  | 1751 | Over1500 | 3.5047 | 2.5644 | 1.8806 | 32.6359 | 17.4058 | 19.238 | 273143 | 213951 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1DX | SA181DX | sa18 1dx | sa181dx | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267547 | 213526 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1DY | SA181DY | sa18 1dy | sa181dy | Carmarthenshire |  | Garnswllt |  | 1749 | Over1500 | 3.5007 | 2.5615 | 1.8784 | 32.5986 | 17.3859 | 19.216 | 269983 | 211798 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1DZ | SA181DZ | sa18 1dz | sa181dz | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267378 | 213589 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1ED | SA181ED | sa18 1ed | sa181ed | Carmarthenshire |  | Garnswllt |  | 1724 | Over1500 | 3.4507 | 2.5249 | 1.8516 | 32.1327 | 17.1374 | 18.9414 | 272340 | 214145 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1EG | SA181EG | sa18 1eg | sa181eg | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270095 | 212182 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1EH | SA181EH | sa18 1eh | sa181eh | Neath Port Talbot |  | Garnswllt |  | 1644 | Over1500 | 3.2905 | 2.4077 | 1.7656 | 30.6416 | 16.3422 | 18.0624 | 269986 | 212336 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1EJ | SA181EJ | sa18 1ej | sa181ej | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267130 | 213525 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1EL | SA181EL | sa18 1el | sa181el | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270064 | 212378 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1EN | SA181EN | sa18 1en | sa181en | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270159 | 212576 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1EP | SA181EP | sa18 1ep | sa181ep | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270098 | 212449 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1EQ | SA181EQ | sa18 1eq | sa181eq | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267349 | 213504 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1ER | SA181ER | sa18 1er | sa181er | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270129 | 212355 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1ES | SA181ES | sa18 1es | sa181es | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270120 | 212270 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1ET | SA181ET | sa18 1et | sa181et | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270164 | 212238 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1EW | SA181EW | sa18 1ew | sa181ew | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270182 | 212464 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1EX | SA181EX | sa18 1ex | sa181ex | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267015 | 213382 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1EY | SA181EY | sa18 1ey | sa181ey | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270125 | 212050 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1EZ | SA181EZ | sa18 1ez | sa181ez | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266977 | 213304 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1HA | SA181HA | sa18 1ha | sa181ha | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270141 | 211964 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HB | SA181HB | sa18 1hb | sa181hb | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270208 | 212007 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HD | SA181HD | sa18 1hd | sa181hd | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270200 | 211873 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HE | SA181HE | sa18 1he | sa181he | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270169 | 211810 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HF | SA181HF | sa18 1hf | sa181hf | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270249 | 211796 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HG | SA181HG | sa18 1hg | sa181hg | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270320 | 211876 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HH | SA181HH | sa18 1hh | sa181hh | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270211 | 211766 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HJ | SA181HJ | sa18 1hj | sa181hj | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266948 | 213023 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1HL | SA181HL | sa18 1hl | sa181hl | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270428 | 211850 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HN | SA181HN | sa18 1hn | sa181hn | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270374 | 211510 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HP | SA181HP | sa18 1hp | sa181hp | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270309 | 211660 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HQ | SA181HQ | sa18 1hq | sa181hq | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267056 | 213076 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1HR | SA181HR | sa18 1hr | sa181hr | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270543 | 211710 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HS | SA181HS | sa18 1hs | sa181hs | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270579 | 211836 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HT | SA181HT | sa18 1ht | sa181ht | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270598 | 211789 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HU | SA181HU | sa18 1hu | sa181hu | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270726 | 211830 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HW | SA181HW | sa18 1hw | sa181hw | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270345 | 211625 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HX | SA181HX | sa18 1hx | sa181hx | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266809 | 213289 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1HY | SA181HY | sa18 1hy | sa181hy | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270510 | 211893 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1HZ | SA181HZ | sa18 1hz | sa181hz | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266892 | 213373 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1JA | SA181JA | sa18 1ja | sa181ja | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266888 | 213284 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1JB | SA181JB | sa18 1jb | sa181jb | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266949 | 213518 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1JD | SA181JD | sa18 1jd | sa181jd | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267089 | 213292 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1JE | SA181JE | sa18 1je | sa181je | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267175 | 213352 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1JF | SA181JF | sa18 1jf | sa181jf | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267078 | 213400 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1JG | SA181JG | sa18 1jg | sa181jg | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268697 | 213402 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1JH | SA181JH | sa18 1jh | sa181jh | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268984 | 213691 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1JJ | SA181JJ | sa18 1jj | sa181jj | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268964 | 213531 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1JL | SA181JL | sa18 1jl | sa181jl | Carmarthenshire |  | Garnswllt |  | 1603 | Over1500 | 3.2085 | 2.3477 | 1.7216 | 29.8774 | 15.9346 | 17.6119 | 269111 | 213660 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1JN | SA181JN | sa18 1jn | sa181jn | Carmarthenshire |  | Garnswllt |  | 1603 | Over1500 | 3.2085 | 2.3477 | 1.7216 | 29.8774 | 15.9346 | 17.6119 | 269203 | 213484 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1JQ | SA181JQ | sa18 1jq | sa181jq | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268890 | 213568 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1JW | SA181JW | sa18 1jw | sa181jw | Carmarthenshire |  | Garnswllt |  | 1603 | Over1500 | 3.2085 | 2.3477 | 1.7216 | 29.8774 | 15.9346 | 17.6119 | 269518 | 213568 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LB | SA181LB | sa18 1lb | sa181lb | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268376 | 213364 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LD | SA181LD | sa18 1ld | sa181ld | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268177 | 213385 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LE | SA181LE | sa18 1le | sa181le | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268298 | 213387 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LF | SA181LF | sa18 1lf | sa181lf | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268405 | 213341 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LG | SA181LG | sa18 1lg | sa181lg | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268497 | 213288 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LH | SA181LH | sa18 1lh | sa181lh | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268515 | 213225 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LL | SA181LL | sa18 1ll | sa181ll | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268361 | 213186 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LN | SA181LN | sa18 1ln | sa181ln | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268152 | 213241 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LP | SA181LP | sa18 1lp | sa181lp | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268184 | 213348 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LQ | SA181LQ | sa18 1lq | sa181lq | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267514 | 213671 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LS | SA181LS | sa18 1ls | sa181ls | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268332 | 213285 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LU | SA181LU | sa18 1lu | sa181lu | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268582 | 213251 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LW | SA181LW | sa18 1lw | sa181lw | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268168 | 213292 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LX | SA181LX | sa18 1lx | sa181lx | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267367 | 213713 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LY | SA181LY | sa18 1ly | sa181ly | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268622 | 213096 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1LZ | SA181LZ | sa18 1lz | sa181lz | BBNPA |  | Nantgwineu |  | 1685 | Over1500 | 3.3726 | 2.4677 | 1.8097 | 31.4058 | 16.7497 | 18.5129 | 269639 | 214698 | Brecon Beacons National Park LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA18 1NA | SA181NA | sa18 1na | sa181na | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268681 | 213064 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1NB | SA181NB | sa18 1nb | sa181nb | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268719 | 213142 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1ND | SA181ND | sa18 1nd | sa181nd | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268965 | 213091 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1NE | SA181NE | sa18 1ne | sa181ne | Carmarthenshire |  | Garnswllt |  | 1603 | Over1500 | 3.2085 | 2.3477 | 1.7216 | 29.8774 | 15.9346 | 17.6119 | 269085 | 213238 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1NF | SA181NF | sa18 1nf | sa181nf | Carmarthenshire |  | Garnswllt |  | 1603 | Over1500 | 3.2085 | 2.3477 | 1.7216 | 29.8774 | 15.9346 | 17.6119 | 269132 | 213095 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1NH | SA181NH | sa18 1nh | sa181nh | Carmarthenshire |  | Garnswllt |  | 1603 | Over1500 | 3.2085 | 2.3477 | 1.7216 | 29.8774 | 15.9346 | 17.6119 | 269368 | 213009 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1NJ | SA181NJ | sa18 1nj | sa181nj | Carmarthenshire |  | Garnswllt |  | 1644 | Over1500 | 3.2905 | 2.4077 | 1.7656 | 30.6416 | 16.3422 | 18.0624 | 269114 | 212735 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1NN | SA181NN | sa18 1nn | sa181nn | Carmarthenshire |  | Garnswllt |  | 1603 | Over1500 | 3.2085 | 2.3477 | 1.7216 | 29.8774 | 15.9346 | 17.6119 | 269133 | 213022 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1NP | SA181NP | sa18 1np | sa181np | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268944 | 212986 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1NS | SA181NS | sa18 1ns | sa181ns | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268890 | 213189 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1NW | SA181NW | sa18 1nw | sa181nw | Carmarthenshire |  | Garnswllt |  | 1644 | Over1500 | 3.2905 | 2.4077 | 1.7656 | 30.6416 | 16.3422 | 18.0624 | 269058 | 212862 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1NZ | SA181NZ | sa18 1nz | sa181nz | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270404 | 211296 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PA | SA181PA | sa18 1pa | sa181pa | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270238 | 211292 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PB | SA181PB | sa18 1pb | sa181pb | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270397 | 211744 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PD | SA181PD | sa18 1pd | sa181pd | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270403 | 211584 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PE | SA181PE | sa18 1pe | sa181pe | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270452 | 211342 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PF | SA181PF | sa18 1pf | sa181pf | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270423 | 211344 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PG | SA181PG | sa18 1pg | sa181pg | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270630 | 211325 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PH | SA181PH | sa18 1ph | sa181ph | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270733 | 211512 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PL | SA181PL | sa18 1pl | sa181pl | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270815 | 211612 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PN | SA181PN | sa18 1pn | sa181pn | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270808 | 211520 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PR | SA181PR | sa18 1pr | sa181pr | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270920 | 211145 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PS | SA181PS | sa18 1ps | sa181ps | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270638 | 211113 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PT | SA181PT | sa18 1pt | sa181pt | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270466 | 211177 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PU | SA181PU | sa18 1pu | sa181pu | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270365 | 211015 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1PY | SA181PY | sa18 1py | sa181py | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270480 | 210982 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RA | SA181RA | sa18 1ra | sa181ra | Neath Port Talbot |  | Garnswllt |  | 1691 | Over1500 | 3.3846 | 2.4765 | 1.8161 | 31.5176 | 16.8094 | 18.5788 | 270593 | 211066 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RB | SA181RB | sa18 1rb | sa181rb | Neath Port Talbot |  | Garnswllt |  | 1759 | Over1500 | 3.5207 | 2.5761 | 1.8892 | 32.785 | 17.4853 | 19.3259 | 270533 | 210756 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RD | SA181RD | sa18 1rd | sa181rd | Neath Port Talbot |  | Garnswllt |  | 1759 | Over1500 | 3.5207 | 2.5761 | 1.8892 | 32.785 | 17.4853 | 19.3259 | 270556 | 210869 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RE | SA181RE | sa18 1re | sa181re | Neath Port Talbot |  | Garnswllt |  | 1759 | Over1500 | 3.5207 | 2.5761 | 1.8892 | 32.785 | 17.4853 | 19.3259 | 270655 | 210868 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RF | SA181RF | sa18 1rf | sa181rf | Neath Port Talbot |  | Garnswllt |  | 1759 | Over1500 | 3.5207 | 2.5761 | 1.8892 | 32.785 | 17.4853 | 19.3259 | 270399 | 210524 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RG | SA181RG | sa18 1rg | sa181rg | Neath Port Talbot |  | Garnswllt |  | 1759 | Over1500 | 3.5207 | 2.5761 | 1.8892 | 32.785 | 17.4853 | 19.3259 | 270527 | 210514 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RL | SA181RL | sa18 1rl | sa181rl | Neath Port Talbot |  | Garnswllt |  | 1759 | Over1500 | 3.5207 | 2.5761 | 1.8892 | 32.785 | 17.4853 | 19.3259 | 270530 | 210404 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RN | SA181RN | sa18 1rn | sa181rn | Neath Port Talbot |  | Garnswllt |  | 1759 | Over1500 | 3.5207 | 2.5761 | 1.8892 | 32.785 | 17.4853 | 19.3259 | 270381 | 210249 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RP | SA181RP | sa18 1rp | sa181rp | Neath Port Talbot |  | Garnswllt |  | 1793 | Over1500 | 3.5888 | 2.6259 | 1.9257 | 33.4187 | 17.8233 | 19.6994 | 270299 | 209803 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RR | SA181RR | sa18 1rr | sa181rr | Neath Port Talbot |  | Garnswllt |  | 1759 | Over1500 | 3.5207 | 2.5761 | 1.8892 | 32.785 | 17.4853 | 19.3259 | 270434 | 210751 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RS | SA181RS | sa18 1rs | sa181rs | Neath Port Talbot |  | Garnswllt |  | 1759 | Over1500 | 3.5207 | 2.5761 | 1.8892 | 32.785 | 17.4853 | 19.3259 | 270361 | 210313 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RU | SA181RU | sa18 1ru | sa181ru | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270243 | 212860 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1RW | SA181RW | sa18 1rw | sa181rw | Neath Port Talbot |  | Garnswllt |  | 1793 | Over1500 | 3.5888 | 2.6259 | 1.9257 | 33.4187 | 17.8233 | 19.6994 | 270382 | 209786 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1SA | SA181SA | sa18 1sa | sa181sa | Carmarthenshire |  | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271201 | 214192 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1SB | SA181SB | sa18 1sb | sa181sb | Carmarthenshire |  | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271119 | 213996 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1SD | SA181SD | sa18 1sd | sa181sd | Carmarthenshire |  | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271118 | 214152 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1SE | SA181SE | sa18 1se | sa181se | Carmarthenshire |  | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271131 | 214228 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1SF | SA181SF | sa18 1sf | sa181sf | Carmarthenshire |  | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271306 | 214173 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1SG | SA181SG | sa18 1sg | sa181sg | Carmarthenshire |  | Garnswllt |  | 1700 | Over1500 | 3.4026 | 2.4897 | 1.8258 | 31.6853 | 16.8988 | 18.6777 | 271181 | 213990 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1SH | SA181SH | sa18 1sh | sa181sh | Carmarthenshire |  | Garnswllt |  | 1709 | Over1500 | 3.4206 | 2.5029 | 1.8355 | 31.8531 | 16.9883 | 18.7766 | 271269 | 213965 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1SJ | SA181SJ | sa18 1sj | sa181sj | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270826 | 213701 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1SL | SA181SL | sa18 1sl | sa181sl | Neath Port Talbot |  | Garnswllt |  | 1709 | Over1500 | 3.4206 | 2.5029 | 1.8355 | 31.8531 | 16.9883 | 18.7766 | 271326 | 213862 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1SN | SA181SN | sa18 1sn | sa181sn | Neath Port Talbot |  | Garnswllt |  | 1709 | Over1500 | 3.4206 | 2.5029 | 1.8355 | 31.8531 | 16.9883 | 18.7766 | 271438 | 213870 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1SP | SA181SP | sa18 1sp | sa181sp | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270853 | 213634 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1SR | SA181SR | sa18 1sr | sa181sr | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270727 | 213616 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1SS | SA181SS | sa18 1ss | sa181ss | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270617 | 213626 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1ST | SA181ST | sa18 1st | sa181st | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270591 | 213589 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1SU | SA181SU | sa18 1su | sa181su | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270694 | 213532 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1SW | SA181SW | sa18 1sw | sa181sw | Neath Port Talbot |  | Garnswllt |  | 1709 | Over1500 | 3.4206 | 2.5029 | 1.8355 | 31.8531 | 16.9883 | 18.7766 | 271107 | 213674 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1SX | SA181SX | sa18 1sx | sa181sx | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270967 | 213559 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1SY | SA181SY | sa18 1sy | sa181sy | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270592 | 213468 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TA | SA181TA | sa18 1ta | sa181ta | Carmarthenshire |  | Garnswllt |  | 1709 | Over1500 | 3.4206 | 2.5029 | 1.8355 | 31.8531 | 16.9883 | 18.7766 | 271035 | 213899 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1TB | SA181TB | sa18 1tb | sa181tb | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270634 | 213396 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TE | SA181TE | sa18 1te | sa181te | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270869 | 213394 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TF | SA181TF | sa18 1tf | sa181tf | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270799 | 213486 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TG | SA181TG | sa18 1tg | sa181tg | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270707 | 213383 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TL | SA181TL | sa18 1tl | sa181tl | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270641 | 213153 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TN | SA181TN | sa18 1tn | sa181tn | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270706 | 213168 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TP | SA181TP | sa18 1tp | sa181tp | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270498 | 213021 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TR | SA181TR | sa18 1tr | sa181tr | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270466 | 213026 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TS | SA181TS | sa18 1ts | sa181ts | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270342 | 212927 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TT | SA181TT | sa18 1tt | sa181tt | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270386 | 212832 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TU | SA181TU | sa18 1tu | sa181tu | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270551 | 212954 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TW | SA181TW | sa18 1tw | sa181tw | Neath Port Talbot |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 270586 | 213165 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1TY | SA181TY | sa18 1ty | sa181ty | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270593 | 212949 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1UF | SA181UF | sa18 1uf | sa181uf | Neath Port Talbot |  | Garnswllt |  | 1603 | Over1500 | 3.2085 | 2.3477 | 1.7216 | 29.8774 | 15.9346 | 17.6119 | 269489 | 213148 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1UG | SA181UG | sa18 1ug | sa181ug | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270084 | 212869 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1UH | SA181UH | sa18 1uh | sa181uh | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270085 | 212822 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1UN | SA181UN | sa18 1un | sa181un | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270762 | 212138 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1UP | SA181UP | sa18 1up | sa181up | Neath Port Talbot |  | Garnswllt |  | 1728 | Over1500 | 3.4587 | 2.5307 | 1.8559 | 32.2072 | 17.1772 | 18.9853 | 271529 | 212134 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1UT | SA181UT | sa18 1ut | sa181ut | Neath Port Talbot |  | Garnswllt |  | 1767 | Over1500 | 3.5367 | 2.5878 | 1.8978 | 32.9341 | 17.5649 | 19.4138 | 271458 | 211972 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1UU | SA181UU | sa18 1uu | sa181uu | Neath Port Talbot |  | Garnswllt |  | 1767 | Over1500 | 3.5367 | 2.5878 | 1.8978 | 32.9341 | 17.5649 | 19.4138 | 271643 | 211920 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1UW | SA181UW | sa18 1uw | sa181uw | Neath Port Talbot |  | Garnswllt |  | 1688 | Over1500 | 3.3786 | 2.4721 | 1.8129 | 31.4617 | 16.7796 | 18.5458 | 270849 | 212057 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1UY | SA181UY | sa18 1uy | sa181uy | Neath Port Talbot |  | Garnswllt |  | 1767 | Over1500 | 3.5367 | 2.5878 | 1.8978 | 32.9341 | 17.5649 | 19.4138 | 271561 | 211882 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1XY | SA181XY | sa18 1xy | sa181xy | Carmarthenshire |  | Garnswllt |  | 1644 | Over1500 | 3.2905 | 2.4077 | 1.7656 | 30.6416 | 16.3422 | 18.0624 | 269174 | 212857 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1YA | SA181YA | sa18 1ya | sa181ya | Neath Port Talbot |  | Garnswllt |  | 1728 | Over1500 | 3.4587 | 2.5307 | 1.8559 | 32.2072 | 17.1772 | 18.9853 | 271848 | 212155 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1YB | SA181YB | sa18 1yb | sa181yb | Neath Port Talbot |  | Garnswllt |  | 1728 | Over1500 | 3.4587 | 2.5307 | 1.8559 | 32.2072 | 17.1772 | 18.9853 | 271851 | 212107 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1YD | SA181YD | sa18 1yd | sa181yd | Neath Port Talbot |  | Garnswllt |  | 1728 | Over1500 | 3.4587 | 2.5307 | 1.8559 | 32.2072 | 17.1772 | 18.9853 | 271972 | 211998 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1YE | SA181YE | sa18 1ye | sa181ye | Neath Port Talbot |  | Garnswllt |  | 1728 | Over1500 | 3.4587 | 2.5307 | 1.8559 | 32.2072 | 17.1772 | 18.9853 | 271886 | 212196 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1YF | SA181YF | sa18 1yf | sa181yf | Neath Port Talbot |  | Garnswllt |  | 1728 | Over1500 | 3.4587 | 2.5307 | 1.8559 | 32.2072 | 17.1772 | 18.9853 | 271928 | 212212 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1YG | SA181YG | sa18 1yg | sa181yg | Neath Port Talbot |  | Garnswllt |  | 1728 | Over1500 | 3.4587 | 2.5307 | 1.8559 | 32.2072 | 17.1772 | 18.9853 | 271981 | 212137 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1YH | SA181YH | sa18 1yh | sa181yh | Neath Port Talbot |  | Garnswllt |  | 1728 | Over1500 | 3.4587 | 2.5307 | 1.8559 | 32.2072 | 17.1772 | 18.9853 | 272006 | 212089 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1YL | SA181YL | sa18 1yl | sa181yl | Neath Port Talbot |  | Garnswllt |  | 1875 | Over1500 | 3.7529 | 2.746 | 2.0137 | 34.9471 | 18.6384 | 20.6004 | 272218 | 211880 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1YN | SA181YN | sa18 1yn | sa181yn | Neath Port Talbot |  | Garnswllt |  | 1875 | Over1500 | 3.7529 | 2.746 | 2.0137 | 34.9471 | 18.6384 | 20.6004 | 272353 | 211760 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA18 1YP | SA181YP | sa18 1yp | sa181yp | Carmarthenshire |  | Garnswllt |  | 1644 | Over1500 | 3.2905 | 2.4077 | 1.7656 | 30.6416 | 16.3422 | 18.0624 | 269226 | 212932 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1YR | SA181YR | sa18 1yr | sa181yr | Carmarthenshire |  | Garnswllt |  | 1644 | Over1500 | 3.2905 | 2.4077 | 1.7656 | 30.6416 | 16.3422 | 18.0624 | 269293 | 212562 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 1YS | SA181YS | sa18 1ys | sa181ys | Carmarthenshire |  | Garnswllt |  | 1644 | Over1500 | 3.2905 | 2.4077 | 1.7656 | 30.6416 | 16.3422 | 18.0624 | 269254 | 212057 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AB | SA182AB | sa18 2ab | sa182ab | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268438 | 213771 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AE | SA182AE | sa18 2ae | sa182ae | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266649 | 213114 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AF | SA182AF | sa18 2af | sa182af | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266400 | 213177 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AH | SA182AH | sa18 2ah | sa182ah | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266577 | 213181 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AJ | SA182AJ | sa18 2aj | sa182aj | Carmarthenshire |  | Garnswllt |  | 1625 | Over1500 | 3.2525 | 2.3799 | 1.7452 | 30.2874 | 16.1533 | 17.8537 | 266930 | 214012 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AL | SA182AL | sa18 2al | sa182al | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268197 | 213684 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AN | SA182AN | sa18 2an | sa182an | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266583 | 213255 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AP | SA182AP | sa18 2ap | sa182ap | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266835 | 213886 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AR | SA182AR | sa18 2ar | sa182ar | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266796 | 213902 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AS | SA182AS | sa18 2as | sa182as | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264219 | 212489 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AT | SA182AT | sa18 2at | sa182at | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268079 | 213711 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AU | SA182AU | sa18 2au | sa182au | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266863 | 213953 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AW | SA182AW | sa18 2aw | sa182aw | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266871 | 213825 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AX | SA182AX | sa18 2ax | sa182ax | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267545 | 213908 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2AY | SA182AY | sa18 2ay | sa182ay | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266935 | 213904 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BA | SA182BA | sa18 2ba | sa182ba | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266946 | 213834 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BB | SA182BB | sa18 2bb | sa182bb | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266952 | 213793 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BD | SA182BD | sa18 2bd | sa182bd | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268712 | 213427 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BE | SA182BE | sa18 2be | sa182be | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266700 | 213211 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BH | SA182BH | sa18 2bh | sa182bh | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262826 | 213244 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BL | SA182BL | sa18 2bl | sa182bl | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268744 | 213630 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council