SA18 2BN | SA182BN | sa18 2bn | sa182bn | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268584 | 213595 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BP | SA182BP | sa18 2bp | sa182bp | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268431 | 213691 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BQ | SA182BQ | sa18 2bq | sa182bq | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267478 | 213934 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BR | SA182BR | sa18 2br | sa182br | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262712 | 212677 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BT | SA182BT | sa18 2bt | sa182bt | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262661 | 212804 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BU | SA182BU | sa18 2bu | sa182bu | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262767 | 212639 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BW | SA182BW | sa18 2bw | sa182bw | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268616 | 213683 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BX | SA182BX | sa18 2bx | sa182bx | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268144 | 213823 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BY | SA182BY | sa18 2by | sa182by | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262857 | 212607 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2BZ | SA182BZ | sa18 2bz | sa182bz | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268410 | 213792 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DA | SA182DA | sa18 2da | sa182da | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262870 | 212873 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DB | SA182DB | sa18 2db | sa182db | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262528 | 212742 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DD | SA182DD | sa18 2dd | sa182dd | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262466 | 212683 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DE | SA182DE | sa18 2de | sa182de | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262426 | 212755 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DF | SA182DF | sa18 2df | sa182df | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262453 | 212782 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DG | SA182DG | sa18 2dg | sa182dg | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262531 | 212794 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DH | SA182DH | sa18 2dh | sa182dh | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262477 | 212866 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DL | SA182DL | sa18 2dl | sa182dl | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262432 | 212874 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DN | SA182DN | sa18 2dn | sa182dn | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262485 | 212957 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DP | SA182DP | sa18 2dp | sa182dp | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262589 | 212964 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DR | SA182DR | sa18 2dr | sa182dr | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262668 | 213046 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DS | SA182DS | sa18 2ds | sa182ds | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262783 | 213114 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DT | SA182DT | sa18 2dt | sa182dt | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262718 | 213048 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DU | SA182DU | sa18 2du | sa182du | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262741 | 212958 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DW | SA182DW | sa18 2dw | sa182dw | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262542 | 212961 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2DY | SA182DY | sa18 2dy | sa182dy | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262790 | 213021 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EA | SA182EA | sa18 2ea | sa182ea | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262797 | 213176 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EB | SA182EB | sa18 2eb | sa182eb | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262766 | 213223 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2ED | SA182ED | sa18 2ed | sa182ed | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262635 | 213168 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EE | SA182EE | sa18 2ee | sa182ee | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262540 | 213225 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EF | SA182EF | sa18 2ef | sa182ef | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262572 | 213522 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EG | SA182EG | sa18 2eg | sa182eg | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262452 | 213621 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EH | SA182EH | sa18 2eh | sa182eh | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262669 | 213667 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EJ | SA182EJ | sa18 2ej | sa182ej | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262459 | 213068 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EN | SA182EN | sa18 2en | sa182en | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262835 | 213367 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EP | SA182EP | sa18 2ep | sa182ep | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268702 | 213731 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2ER | SA182ER | sa18 2er | sa182er | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268800 | 213756 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2ES | SA182ES | sa18 2es | sa182es | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262713 | 213546 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2ET | SA182ET | sa18 2et | sa182et | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263155 | 211880 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EW | SA182EW | sa18 2ew | sa182ew | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262735 | 213372 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EX | SA182EX | sa18 2ex | sa182ex | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263228 | 211935 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EY | SA182EY | sa18 2ey | sa182ey | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263460 | 212037 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2EZ | SA182EZ | sa18 2ez | sa182ez | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263031 | 211653 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2FA | SA182FA | sa18 2fa | sa182fa | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268146 | 213637 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2FB | SA182FB | sa18 2fb | sa182fb | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263924 | 211435 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2FD | SA182FD | sa18 2fd | sa182fd | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262913 | 213361 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2FE | SA182FE | sa18 2fe | sa182fe | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262837 | 213674 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2FF | SA182FF | sa18 2ff | sa182ff | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264376 | 212077 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2FG | SA182FG | sa18 2fg | sa182fg | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264350 | 211985 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2FL | SA182FL | sa18 2fl | sa182fl | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264397 | 211890 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2FN | SA182FN | sa18 2fn | sa182fn | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264242 | 212687 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2FP | SA182FP | sa18 2fp | sa182fp | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264043 | 212410 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2FQ | SA182FQ | sa18 2fq | sa182fq | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 262060 | 215347 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2GA | SA182GA | sa18 2ga | sa182ga | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262990 | 213565 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2GB | SA182GB | sa18 2gb | sa182gb | Carmarthenshire |  | Garnswllt |  | 1562 | Over1500 | 3.1264 | 2.2876 | 1.6776 | 29.1132 | 15.5271 | 17.1615 | 268743 | 213547 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2GD | SA182GD | sa18 2gd | sa182gd | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264460 | 211919 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2GE | SA182GE | sa18 2ge | sa182ge | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262892 | 213563 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2GF | SA182GF | sa18 2gf | sa182gf | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262633 | 213489 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2GX | SA182GX | sa18 2gx | sa182gx | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264436 | 212438 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2GY | SA182GY | sa18 2gy | sa182gy | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263685 | 211448 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HA | SA182HA | sa18 2ha | sa182ha | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263534 | 211977 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HB | SA182HB | sa18 2hb | sa182hb | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263328 | 211777 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HD | SA182HD | sa18 2hd | sa182hd | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263661 | 211824 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HE | SA182HE | sa18 2he | sa182he | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263201 | 211694 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HF | SA182HF | sa18 2hf | sa182hf | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263395 | 211367 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HG | SA182HG | sa18 2hg | sa182hg | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263083 | 211415 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HH | SA182HH | sa18 2hh | sa182hh | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263205 | 211465 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HJ | SA182HJ | sa18 2hj | sa182hj | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264192 | 212391 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HL | SA182HL | sa18 2hl | sa182hl | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263286 | 211579 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HN | SA182HN | sa18 2hn | sa182hn | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263303 | 211650 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HP | SA182HP | sa18 2hp | sa182hp | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263590 | 211524 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HQ | SA182HQ | sa18 2hq | sa182hq | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264017 | 212424 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HR | SA182HR | sa18 2hr | sa182hr | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263532 | 211605 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HS | SA182HS | sa18 2hs | sa182hs | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263846 | 211187 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HT | SA182HT | sa18 2ht | sa182ht | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263569 | 211404 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HU | SA182HU | sa18 2hu | sa182hu | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263982 | 211387 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HW | SA182HW | sa18 2hw | sa182hw | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263730 | 211474 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HX | SA182HX | sa18 2hx | sa182hx | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264379 | 212666 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HY | SA182HY | sa18 2hy | sa182hy | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264083 | 211467 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2HZ | SA182HZ | sa18 2hz | sa182hz | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264589 | 212624 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JA | SA182JA | sa18 2ja | sa182ja | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264583 | 212550 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JB | SA182JB | sa18 2jb | sa182jb | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264738 | 212670 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JD | SA182JD | sa18 2jd | sa182jd | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264793 | 212779 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JE | SA182JE | sa18 2je | sa182je | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264928 | 212505 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JG | SA182JG | sa18 2jg | sa182jg | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 266165 | 213133 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JL | SA182JL | sa18 2jl | sa182jl | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264673 | 212463 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JN | SA182JN | sa18 2jn | sa182jn | Carmarthenshire |  | Garnswllt |  | 1564 | Over1500 | 3.1304 | 2.2905 | 1.6797 | 29.1505 | 15.5469 | 17.1835 | 265122 | 212138 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JP | SA182JP | sa18 2jp | sa182jp | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264297 | 212719 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JQ | SA182JQ | sa18 2jq | sa182jq | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263598 | 211557 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JR | SA182JR | sa18 2jr | sa182jr | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264646 | 212414 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JS | SA182JS | sa18 2js | sa182js | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264268 | 212575 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JT | SA182JT | sa18 2jt | sa182jt | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264293 | 212542 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JU | SA182JU | sa18 2ju | sa182ju | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264153 | 212457 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JW | SA182JW | sa18 2jw | sa182jw | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264742 | 212549 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JX | SA182JX | sa18 2jx | sa182jx | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262174 | 214915 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JY | SA182JY | sa18 2jy | sa182jy | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262205 | 214814 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2JZ | SA182JZ | sa18 2jz | sa182jz | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264190 | 212276 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LA | SA182LA | sa18 2la | sa182la | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264109 | 211530 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LB | SA182LB | sa18 2lb | sa182lb | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264113 | 211651 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LD | SA182LD | sa18 2ld | sa182ld | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264115 | 211685 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LE | SA182LE | sa18 2le | sa182le | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264176 | 211677 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LF | SA182LF | sa18 2lf | sa182lf | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264137 | 211973 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LG | SA182LG | sa18 2lg | sa182lg | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262288 | 212811 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LH | SA182LH | sa18 2lh | sa182lh | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263534 | 211332 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LL | SA182LL | sa18 2ll | sa182ll | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263168 | 212316 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LN | SA182LN | sa18 2ln | sa182ln | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262968 | 212397 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LP | SA182LP | sa18 2lp | sa182lp | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262224 | 212813 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LR | SA182LR | sa18 2lr | sa182lr | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262897 | 211726 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LS | SA182LS | sa18 2ls | sa182ls | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263232 | 212128 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LT | SA182LT | sa18 2lt | sa182lt | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263154 | 212124 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LU | SA182LU | sa18 2lu | sa182lu | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263198 | 212213 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LW | SA182LW | sa18 2lw | sa182lw | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262135 | 212840 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LY | SA182LY | sa18 2ly | sa182ly | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263051 | 212334 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NA | SA182NA | sa18 2na | sa182na | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263069 | 212316 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NB | SA182NB | sa18 2nb | sa182nb | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263304 | 212381 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2ND | SA182ND | sa18 2nd | sa182nd | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263664 | 212521 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NE | SA182NE | sa18 2ne | sa182ne | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263970 | 212858 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NF | SA182NF | sa18 2nf | sa182nf | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263758 | 212668 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NG | SA182NG | sa18 2ng | sa182ng | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263630 | 212573 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NH | SA182NH | sa18 2nh | sa182nh | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263501 | 212556 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NL | SA182NL | sa18 2nl | sa182nl | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263371 | 212519 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NN | SA182NN | sa18 2nn | sa182nn | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263346 | 212597 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NP | SA182NP | sa18 2np | sa182np | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263072 | 212517 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NR | SA182NR | sa18 2nr | sa182nr | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262993 | 212656 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NS | SA182NS | sa18 2ns | sa182ns | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263138 | 212381 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NT | SA182NT | sa18 2nt | sa182nt | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263083 | 212046 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NU | SA182NU | sa18 2nu | sa182nu | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262229 | 212730 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NW | SA182NW | sa18 2nw | sa182nw | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263155 | 212679 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NY | SA182NY | sa18 2ny | sa182ny | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262208 | 214333 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PA | SA182PA | sa18 2pa | sa182pa | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264279 | 211769 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PB | SA182PB | sa18 2pb | sa182pb | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264321 | 211589 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PD | SA182PD | sa18 2pd | sa182pd | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264566 | 211468 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PE | SA182PE | sa18 2pe | sa182pe | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264629 | 211292 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PF | SA182PF | sa18 2pf | sa182pf | Carmarthenshire |  | Garnswllt |  | 1650 | Over1500 | 3.3025 | 2.4165 | 1.7721 | 30.7534 | 16.4018 | 18.1283 | 265190 | 211231 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PG | SA182PG | sa18 2pg | sa182pg | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264373 | 211319 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PH | SA182PH | sa18 2ph | sa182ph | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264297 | 211026 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PJ | SA182PJ | sa18 2pj | sa182pj | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262945 | 212555 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PL | SA182PL | sa18 2pl | sa182pl | Carmarthenshire |  | Garnswllt |  | 1689 | Over1500 | 3.3806 | 2.4736 | 1.814 | 31.4803 | 16.7895 | 18.5568 | 264573 | 210378 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PP | SA182PP | sa18 2pp | sa182pp | Carmarthenshire |  | Garnswllt |  | 1560 | Over1500 | 3.1224 | 2.2847 | 1.6754 | 29.076 | 15.5072 | 17.1395 | 263746 | 210960 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PR | SA182PR | sa18 2pr | sa182pr | Carmarthenshire |  | Garnswllt |  | 1560 | Over1500 | 3.1224 | 2.2847 | 1.6754 | 29.076 | 15.5072 | 17.1395 | 263619 | 210635 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PS | SA182PS | sa18 2ps | sa182ps | Carmarthenshire |  | Garnswllt |  | 1560 | Over1500 | 3.1224 | 2.2847 | 1.6754 | 29.076 | 15.5072 | 17.1395 | 263270 | 210849 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PT | SA182PT | sa18 2pt | sa182pt | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263088 | 211034 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PU | SA182PU | sa18 2pu | sa182pu | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263058 | 211069 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PX | SA182PX | sa18 2px | sa182px | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262987 | 212766 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PY | SA182PY | sa18 2py | sa182py | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263091 | 211218 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2PZ | SA182PZ | sa18 2pz | sa182pz | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264037 | 211892 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2QA | SA182QA | sa18 2qa | sa182qa | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 264340 | 212439 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2QB | SA182QB | sa18 2qb | sa182qb | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262066 | 212888 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2QD | SA182QD | sa18 2qd | sa182qd | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 264193 | 211944 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2QE | SA182QE | sa18 2qe | sa182qe | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262068 | 212989 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2RA | SA182RA | sa18 2ra | sa182ra | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263197 | 211161 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2RB | SA182RB | sa18 2rb | sa182rb | Carmarthenshire |  | Garnswllt |  | 1560 | Over1500 | 3.1224 | 2.2847 | 1.6754 | 29.076 | 15.5072 | 17.1395 | 263131 | 210884 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2RD | SA182RD | sa18 2rd | sa182rd | Carmarthenshire |  | Garnswllt |  | 1482 | 1200-1500 | 2.9663 | 2.1704 | 1.5917 | 27.6222 | 14.7318 | 16.2825 | 262933 | 210436 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2RE | SA182RE | sa18 2re | sa182re | Carmarthenshire |  | Garnswllt |  | 1482 | 1200-1500 | 2.9663 | 2.1704 | 1.5917 | 27.6222 | 14.7318 | 16.2825 | 262598 | 210438 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2RF | SA182RF | sa18 2rf | sa182rf | Carmarthenshire |  | Garnswllt |  | 1482 | 1200-1500 | 2.9663 | 2.1704 | 1.5917 | 27.6222 | 14.7318 | 16.2825 | 262551 | 210340 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2RG | SA182RG | sa18 2rg | sa182rg | Swansea |  | Garnswllt |  | 1482 | 1200-1500 | 2.9663 | 2.1704 | 1.5917 | 27.6222 | 14.7318 | 16.2825 | 262599 | 210076 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA18 2RH | SA182RH | sa18 2rh | sa182rh | Swansea |  | Garnswllt |  | 1482 | 1200-1500 | 2.9663 | 2.1704 | 1.5917 | 27.6222 | 14.7318 | 16.2825 | 262531 | 210084 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA18 2RJ | SA182RJ | sa18 2rj | sa182rj | Swansea |  | Garnswllt |  | 1514 | Over1500 | 3.0303 | 2.2173 | 1.626 | 28.2186 | 15.0499 | 16.6341 | 262710 | 209912 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA18 2RL | SA182RL | sa18 2rl | sa182rl | Swansea |  | Garnswllt |  | 1514 | Over1500 | 3.0303 | 2.2173 | 1.626 | 28.2186 | 15.0499 | 16.6341 | 262391 | 209692 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA18 2RN | SA182RN | sa18 2rn | sa182rn | Swansea |  | Garnswllt |  | 1514 | Over1500 | 3.0303 | 2.2173 | 1.626 | 28.2186 | 15.0499 | 16.6341 | 262715 | 209736 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA18 2RP | SA182RP | sa18 2rp | sa182rp | Swansea |  | Garnswllt |  | 1514 | Over1500 | 3.0303 | 2.2173 | 1.626 | 28.2186 | 15.0499 | 16.6341 | 262567 | 209103 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA18 2RR | SA182RR | sa18 2rr | sa182rr | Swansea |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 262137 | 208610 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA18 2RW | SA182RW | sa18 2rw | sa182rw | Carmarthenshire |  | Garnswllt |  | 1577 | Over1500 | 3.1564 | 2.3096 | 1.6937 | 29.3928 | 15.6762 | 17.3263 | 263268 | 209645 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2RY | SA182RY | sa18 2ry | sa182ry | Swansea |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 262574 | 208924 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA18 2SA | SA182SA | sa18 2sa | sa182sa | Swansea |  | Garnswllt |  | 1514 | Over1500 | 3.0303 | 2.2173 | 1.626 | 28.2186 | 15.0499 | 16.6341 | 262736 | 208999 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA18 2SE | SA182SE | sa18 2se | sa182se | Swansea |  | Garnswllt |  | 1622 | Over1500 | 3.2465 | 2.3755 | 1.742 | 30.2315 | 16.1235 | 17.8207 | 262947 | 208531 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA18 2SG | SA182SG | sa18 2sg | sa182sg | Carmarthenshire |  | Garnswllt |  | 1560 | Over1500 | 3.1224 | 2.2847 | 1.6754 | 29.076 | 15.5072 | 17.1395 | 263609 | 210327 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2SH | SA182SH | sa18 2sh | sa182sh | Carmarthenshire |  | Garnswllt |  | 1560 | Over1500 | 3.1224 | 2.2847 | 1.6754 | 29.076 | 15.5072 | 17.1395 | 264005 | 210294 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2SP | SA182SP | sa18 2sp | sa182sp | Carmarthenshire |  | Garnswllt |  | 1505 | Over1500 | 3.0123 | 2.2041 | 1.6164 | 28.0508 | 14.9604 | 16.5352 | 263263 | 210984 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2SR | SA182SR | sa18 2sr | sa182sr | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262402 | 214490 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2SS | SA182SS | sa18 2ss | sa182ss | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262340 | 214412 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2ST | SA182ST | sa18 2st | sa182st | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262381 | 214232 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2SU | SA182SU | sa18 2su | sa182su | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262265 | 214445 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2SX | SA182SX | sa18 2sx | sa182sx | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262408 | 214359 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2SY | SA182SY | sa18 2sy | sa182sy | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262275 | 214612 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2TA | SA182TA | sa18 2ta | sa182ta | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262514 | 214603 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2TG | SA182TG | sa18 2tg | sa182tg | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 262756 | 215092 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2TH | SA182TH | sa18 2th | sa182th | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 262020 | 215736 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2TJ | SA182TJ | sa18 2tj | sa182tj | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262480 | 214568 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2TL | SA182TL | sa18 2tl | sa182tl | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 262165 | 215693 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2TN | SA182TN | sa18 2tn | sa182tn | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 262261 | 215831 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2TP | SA182TP | sa18 2tp | sa182tp | Carmarthenshire |  | Garnswllt |  | 1594 | Over1500 | 3.1905 | 2.3345 | 1.7119 | 29.7097 | 15.8452 | 17.5131 | 263074 | 216682 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2TQ | SA182TQ | sa18 2tq | sa182tq | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 262035 | 215485 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2TW | SA182TW | sa18 2tw | sa182tw | Carmarthenshire |  | Garnswllt |  | 1545 | Over1500 | 3.0924 | 2.2627 | 1.6593 | 28.7964 | 15.3581 | 16.9747 | 262513 | 216109 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2UG | SA182UG | sa18 2ug | sa182ug | Carmarthenshire |  | Garnswllt |  | 1678 | Over1500 | 3.3586 | 2.4575 | 1.8022 | 31.2753 | 16.6802 | 18.436 | 265135 | 214607 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2UH | SA182UH | sa18 2uh | sa182uh | Carmarthenshire |  | Garnswllt |  | 1595 | Over1500 | 3.1925 | 2.3359 | 1.713 | 29.7283 | 15.8551 | 17.524 | 264891 | 214027 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2UN | SA182UN | sa18 2un | sa182un | Carmarthenshire |  | Garnswllt |  | 1595 | Over1500 | 3.1925 | 2.3359 | 1.713 | 29.7283 | 15.8551 | 17.524 | 264519 | 214076 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2UP | SA182UP | sa18 2up | sa182up | Carmarthenshire |  | Garnswllt |  | 1534 | Over1500 | 3.0704 | 2.2466 | 1.6475 | 28.5914 | 15.2487 | 16.8538 | 263634 | 213885 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2UR | SA182UR | sa18 2ur | sa182ur | Carmarthenshire |  | Garnswllt |  | 1559 | Over1500 | 3.1204 | 2.2832 | 1.6744 | 29.0573 | 15.4972 | 17.1285 | 264160 | 213572 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2US | SA182US | sa18 2us | sa182us | Carmarthenshire |  | Garnswllt |  | 1559 | Over1500 | 3.1204 | 2.2832 | 1.6744 | 29.0573 | 15.4972 | 17.1285 | 264618 | 213283 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2UT | SA182UT | sa18 2ut | sa182ut | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263741 | 212804 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2UW | SA182UW | sa18 2uw | sa182uw | Carmarthenshire |  | Garnswllt |  | 1595 | Over1500 | 3.1925 | 2.3359 | 1.713 | 29.7283 | 15.8551 | 17.524 | 264148 | 214247 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2UY | SA182UY | sa18 2uy | sa182uy | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262210 | 214555 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2YB | SA182YB | sa18 2yb | sa182yb | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267121 | 213816 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2YE | SA182YE | sa18 2ye | sa182ye | Carmarthenshire |  | Garnswllt |  | 1550 | Over1500 | 3.1024 | 2.27 | 1.6647 | 28.8896 | 15.4078 | 17.0296 | 267290 | 213968 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2YF | SA182YF | sa18 2yf | sa182yf | Carmarthenshire |  | Garnswllt |  | 1593 | Over1500 | 3.1885 | 2.333 | 1.7109 | 29.691 | 15.8352 | 17.5021 | 267218 | 214153 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2YH | SA182YH | sa18 2yh | sa182yh | Carmarthenshire |  | Garnswllt |  | 1593 | Over1500 | 3.1885 | 2.333 | 1.7109 | 29.691 | 15.8352 | 17.5021 | 267168 | 214262 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2YL | SA182YL | sa18 2yl | sa182yl | Carmarthenshire |  | Garnswllt |  | 1593 | Over1500 | 3.1885 | 2.333 | 1.7109 | 29.691 | 15.8352 | 17.5021 | 267079 | 214424 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2YN | SA182YN | sa18 2yn | sa182yn | BBNPA |  | Garnswllt |  | 1593 | Over1500 | 3.1885 | 2.333 | 1.7109 | 29.691 | 15.8352 | 17.5021 | 267131 | 214418 | Brecon Beacons National Park LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA18 2YR | SA182YR | sa18 2yr | sa182yr | BBNPA |  | Garnswllt |  | 1625 | Over1500 | 3.2525 | 2.3799 | 1.7452 | 30.2874 | 16.1533 | 17.8537 | 266512 | 214569 | Brecon Beacons National Park LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA18 2YS | SA182YS | sa18 2ys | sa182ys | Carmarthenshire |  | Garnswllt |  | 1625 | Over1500 | 3.2525 | 2.3799 | 1.7452 | 30.2874 | 16.1533 | 17.8537 | 266748 | 214266 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2YT | SA182YT | sa18 2yt | sa182yt | Carmarthenshire |  | Garnswllt |  | 1625 | Over1500 | 3.2525 | 2.3799 | 1.7452 | 30.2874 | 16.1533 | 17.8537 | 266608 | 213987 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2YW | SA182YW | sa18 2yw | sa182yw | BBNPA |  | Garnswllt |  | 1593 | Over1500 | 3.1885 | 2.333 | 1.7109 | 29.691 | 15.8352 | 17.5021 | 267104 | 214440 | Brecon Beacons National Park LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA18 3AB | SA183AB | sa18 3ab | sa183ab | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262949 | 212388 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AF | SA183AF | sa18 3af | sa183af | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262886 | 212426 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AG | SA183AG | sa18 3ag | sa183ag | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262839 | 212510 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AJ | SA183AJ | sa18 3aj | sa183aj | Carmarthenshire |  | Garnswllt |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 261487 | 214867 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AL | SA183AL | sa18 3al | sa183al | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262948 | 212356 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AN | SA183AN | sa18 3an | sa183an | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262682 | 212242 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AP | SA183AP | sa18 3ap | sa183ap | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262436 | 212227 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AQ | SA183AQ | sa18 3aq | sa183aq | Carmarthenshire |  | Garnswllt |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 261542 | 214876 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AR | SA183AR | sa18 3ar | sa183ar | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262531 | 212384 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AS | SA183AS | sa18 3as | sa183as | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262468 | 212541 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AT | SA183AT | sa18 3at | sa183at | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262493 | 212597 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AU | SA183AU | sa18 3au | sa183au | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262608 | 212487 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AW | SA183AW | sa18 3aw | sa183aw | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262515 | 212271 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AX | SA183AX | sa18 3ax | sa183ax | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261581 | 215201 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AY | SA183AY | sa18 3ay | sa183ay | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262707 | 212568 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3AZ | SA183AZ | sa18 3az | sa183az | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261575 | 215361 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BA | SA183BA | sa18 3ba | sa183ba | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262607 | 212617 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BB | SA183BB | sa18 3bb | sa183bb | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262683 | 212508 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BD | SA183BD | sa18 3bd | sa183bd | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262627 | 212424 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BE | SA183BE | sa18 3be | sa183be | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262757 | 212526 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BG | SA183BG | sa18 3bg | sa183bg | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262693 | 212432 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BH | SA183BH | sa18 3bh | sa183bh | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262542 | 212558 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BJ | SA183BJ | sa18 3bj | sa183bj | Carmarthenshire |  | Garnswllt |  | 1581 | Over1500 | 3.1644 | 2.3154 | 1.698 | 29.4674 | 15.7159 | 17.3702 | 259760 | 211845 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BL | SA183BL | sa18 3bl | sa183bl | Carmarthenshire |  | Garnswllt |  | 1581 | Over1500 | 3.1644 | 2.3154 | 1.698 | 29.4674 | 15.7159 | 17.3702 | 259981 | 210997 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BN | SA183BN | sa18 3bn | sa183bn | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261538 | 214993 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BQ | SA183BQ | sa18 3bq | sa183bq | Carmarthenshire |  | Garnswllt |  | 1559 | Over1500 | 3.1204 | 2.2832 | 1.6744 | 29.0573 | 15.4972 | 17.1285 | 260650 | 213851 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BS | SA183BS | sa18 3bs | sa183bs | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263016 | 212212 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BU | SA183BU | sa18 3bu | sa183bu | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261713 | 215561 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BW | SA183BW | sa18 3bw | sa183bw | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263089 | 212261 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BX | SA183BX | sa18 3bx | sa183bx | Carmarthenshire |  | Garnswllt |  | 1559 | Over1500 | 3.1204 | 2.2832 | 1.6744 | 29.0573 | 15.4972 | 17.1285 | 260470 | 213621 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BY | SA183BY | sa18 3by | sa183by | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262964 | 212213 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3BZ | SA183BZ | sa18 3bz | sa183bz | Carmarthenshire |  | Garnswllt |  | 1559 | Over1500 | 3.1204 | 2.2832 | 1.6744 | 29.0573 | 15.4972 | 17.1285 | 260294 | 213775 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DA | SA183DA | sa18 3da | sa183da | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262965 | 212188 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DB | SA183DB | sa18 3db | sa183db | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 263010 | 212289 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DD | SA183DD | sa18 3dd | sa183dd | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262735 | 211844 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DE | SA183DE | sa18 3de | sa183de | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263015 | 212281 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DJ | SA183DJ | sa18 3dj | sa183dj | Carmarthenshire |  | Garnswllt |  | 1600 | Over1500 | 3.2025 | 2.3433 | 1.7184 | 29.8215 | 15.9048 | 17.579 | 259973 | 213683 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DL | SA183DL | sa18 3dl | sa183dl | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262950 | 212330 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DN | SA183DN | sa18 3dn | sa183dn | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262883 | 212262 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DQ | SA183DQ | sa18 3dq | sa183dq | Carmarthenshire |  | Garnswllt |  | 1600 | Over1500 | 3.2025 | 2.3433 | 1.7184 | 29.8215 | 15.9048 | 17.579 | 259990 | 213737 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DR | SA183DR | sa18 3dr | sa183dr | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262752 | 212087 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DS | SA183DS | sa18 3ds | sa183ds | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262646 | 211605 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DT | SA183DT | sa18 3dt | sa183dt | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262728 | 212094 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DU | SA183DU | sa18 3du | sa183du | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262675 | 211983 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DW | SA183DW | sa18 3dw | sa183dw | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262789 | 212095 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DX | SA183DX | sa18 3dx | sa183dx | Carmarthenshire |  | Garnswllt |  | 1600 | Over1500 | 3.2025 | 2.3433 | 1.7184 | 29.8215 | 15.9048 | 17.579 | 259781 | 213688 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DY | SA183DY | sa18 3dy | sa183dy | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262497 | 211925 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3DZ | SA183DZ | sa18 3dz | sa183dz | Carmarthenshire |  | Garnswllt |  | 1600 | Over1500 | 3.2025 | 2.3433 | 1.7184 | 29.8215 | 15.9048 | 17.579 | 259587 | 213574 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EA | SA183EA | sa18 3ea | sa183ea | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262507 | 211889 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EB | SA183EB | sa18 3eb | sa183eb | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262816 | 211940 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3ED | SA183ED | sa18 3ed | sa183ed | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262989 | 212019 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EE | SA183EE | sa18 3ee | sa183ee | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262942 | 211942 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EF | SA183EF | sa18 3ef | sa183ef | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262863 | 212102 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EG | SA183EG | sa18 3eg | sa183eg | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262814 | 212046 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EH | SA183EH | sa18 3eh | sa183eh | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262872 | 212025 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EJ | SA183EJ | sa18 3ej | sa183ej | Carmarthenshire |  | Garnswllt |  | 1616 | Over1500 | 3.2345 | 2.3667 | 1.7356 | 30.1197 | 16.0638 | 17.7548 | 259725 | 214563 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EL | SA183EL | sa18 3el | sa183el | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262994 | 212147 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EN | SA183EN | sa18 3en | sa183en | Carmarthenshire |  | Garnswllt |  | 1497 | 1200-1500 | 2.9963 | 2.1924 | 1.6078 | 27.9017 | 14.8809 | 16.4473 | 263090 | 212142 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EQ | SA183EQ | sa18 3eq | sa183eq | Carmarthenshire |  | Garnswllt |  | 1600 | Over1500 | 3.2025 | 2.3433 | 1.7184 | 29.8215 | 15.9048 | 17.579 | 259891 | 213889 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3ER | SA183ER | sa18 3er | sa183er | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262792 | 211732 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3ES | SA183ES | sa18 3es | sa183es | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262631 | 211878 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EX | SA183EX | sa18 3ex | sa183ex | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262821 | 211860 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EY | SA183EY | sa18 3ey | sa183ey | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262546 | 211662 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3EZ | SA183EZ | sa18 3ez | sa183ez | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262730 | 211643 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3FA | SA183FA | sa18 3fa | sa183fa | Carmarthenshire |  | Garnswllt |  | 1575 | Over1500 | 3.1524 | 2.3067 | 1.6915 | 29.3555 | 15.6563 | 17.3043 | 259736 | 210966 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3FB | SA183FB | sa18 3fb | sa183fb | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262632 | 211685 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3FD | SA183FD | sa18 3fd | sa183fd | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262499 | 212461 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3GA | SA183GA | sa18 3ga | sa183ga | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261034 | 211192 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3GL | SA183GL | sa18 3gl | sa183gl | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262830 | 212481 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3GY | SA183GY | sa18 3gy | sa183gy | Carmarthenshire |  | Garnswllt |  | 1520 | Over1500 | 3.0423 | 2.2261 | 1.6325 | 28.3304 | 15.1096 | 16.7 | 261939 | 217033 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HA | SA183HA | sa18 3ha | sa183ha | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262438 | 211705 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HB | SA183HB | sa18 3hb | sa183hb | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262467 | 211779 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HD | SA183HD | sa18 3hd | sa183hd | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262494 | 211456 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HE | SA183HE | sa18 3he | sa183he | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262433 | 211499 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HF | SA183HF | sa18 3hf | sa183hf | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262342 | 211497 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HG | SA183HG | sa18 3hg | sa183hg | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262383 | 211403 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HH | SA183HH | sa18 3hh | sa183hh | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262410 | 211238 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HJ | SA183HJ | sa18 3hj | sa183hj | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261718 | 215393 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HL | SA183HL | sa18 3hl | sa183hl | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262326 | 211065 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HN | SA183HN | sa18 3hn | sa183hn | Carmarthenshire |  | Garnswllt |  | 1482 | 1200-1500 | 2.9663 | 2.1704 | 1.5917 | 27.6222 | 14.7318 | 16.2825 | 262303 | 210831 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HP | SA183HP | sa18 3hp | sa183hp | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 262009 | 211661 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HS | SA183HS | sa18 3hs | sa183hs | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261954 | 211742 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HW | SA183HW | sa18 3hw | sa183hw | Carmarthenshire |  | Garnswllt |  | 1482 | 1200-1500 | 2.9663 | 2.1704 | 1.5917 | 27.6222 | 14.7318 | 16.2825 | 262266 | 210760 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HX | SA183HX | sa18 3hx | sa183hx | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261783 | 215452 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HY | SA183HY | sa18 3hy | sa183hy | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261651 | 215496 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3HZ | SA183HZ | sa18 3hz | sa183hz | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261846 | 215488 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JA | SA183JA | sa18 3ja | sa183ja | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261687 | 215625 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JB | SA183JB | sa18 3jb | sa183jb | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261537 | 215768 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JD | SA183JD | sa18 3jd | sa183jd | Carmarthenshire |  | Garnswllt |  | 1532 | Over1500 | 3.0664 | 2.2437 | 1.6454 | 28.5541 | 15.2288 | 16.8319 | 261626 | 216120 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JF | SA183JF | sa18 3jf | sa183jf | Carmarthenshire |  | Garnswllt |  | 1532 | Over1500 | 3.0664 | 2.2437 | 1.6454 | 28.5541 | 15.2288 | 16.8319 | 261658 | 216415 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JG | SA183JG | sa18 3jg | sa183jg | Carmarthenshire |  | Garnswllt |  | 1532 | Over1500 | 3.0664 | 2.2437 | 1.6454 | 28.5541 | 15.2288 | 16.8319 | 261919 | 216423 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JH | SA183JH | sa18 3jh | sa183jh | Carmarthenshire |  | Garnswllt |  | 1642 | Over1500 | 3.2865 | 2.4048 | 1.7635 | 30.6043 | 16.3223 | 18.0404 | 260870 | 216154 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JL | SA183JL | sa18 3jl | sa183jl | Carmarthenshire |  | Garnswllt |  | 1642 | Over1500 | 3.2865 | 2.4048 | 1.7635 | 30.6043 | 16.3223 | 18.0404 | 260755 | 216272 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JN | SA183JN | sa18 3jn | sa183jn | Carmarthenshire |  | Garnswllt |  | 1642 | Over1500 | 3.2865 | 2.4048 | 1.7635 | 30.6043 | 16.3223 | 18.0404 | 260758 | 216231 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JQ | SA183JQ | sa18 3jq | sa183jq | Carmarthenshire |  | Garnswllt |  | 1532 | Over1500 | 3.0664 | 2.2437 | 1.6454 | 28.5541 | 15.2288 | 16.8319 | 261456 | 216176 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JS | SA183JS | sa18 3js | sa183js | Carmarthenshire |  | Carmel & Pant-Y-Llyn |  | 1642 | Over1500 | 3.2865 | 2.4048 | 1.7635 | 30.6043 | 16.3223 | 18.0404 | 260603 | 216875 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JT | SA183JT | sa18 3jt | sa183jt | Carmarthenshire |  | Carmel & Pant-Y-Llyn |  | 1642 | Over1500 | 3.2865 | 2.4048 | 1.7635 | 30.6043 | 16.3223 | 18.0404 | 260477 | 216919 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JU | SA183JU | sa18 3ju | sa183ju | Carmarthenshire |  | Carmel & Pant-Y-Llyn |  | 1642 | Over1500 | 3.2865 | 2.4048 | 1.7635 | 30.6043 | 16.3223 | 18.0404 | 260230 | 216914 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JY | SA183JY | sa18 3jy | sa183jy | Carmarthenshire |  | Carmel & Pant-Y-Llyn |  | 1568 | Over1500 | 3.1384 | 2.2964 | 1.684 | 29.2251 | 15.5867 | 17.2274 | 260565 | 217447 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3JZ | SA183JZ | sa18 3jz | sa183jz | Carmarthenshire |  | Garnswllt |  | 1520 | Over1500 | 3.0423 | 2.2261 | 1.6325 | 28.3304 | 15.1096 | 16.7 | 261524 | 217136 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LA | SA183LA | sa18 3la | sa183la | Carmarthenshire |  | Garnswllt |  | 1547 | Over1500 | 3.0964 | 2.2656 | 1.6615 | 28.8337 | 15.3779 | 16.9967 | 260435 | 211072 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LB | SA183LB | sa18 3lb | sa183lb | Carmarthenshire |  | Garnswllt |  | 1547 | Over1500 | 3.0964 | 2.2656 | 1.6615 | 28.8337 | 15.3779 | 16.9967 | 260376 | 211321 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LD | SA183LD | sa18 3ld | sa183ld | Carmarthenshire |  | Garnswllt |  | 1547 | Over1500 | 3.0964 | 2.2656 | 1.6615 | 28.8337 | 15.3779 | 16.9967 | 260281 | 211199 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LE | SA183LE | sa18 3le | sa183le | Carmarthenshire |  | Garnswllt |  | 1581 | Over1500 | 3.1644 | 2.3154 | 1.698 | 29.4674 | 15.7159 | 17.3702 | 259855 | 211230 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LF | SA183LF | sa18 3lf | sa183lf | Carmarthenshire |  | Garnswllt |  | 1581 | Over1500 | 3.1644 | 2.3154 | 1.698 | 29.4674 | 15.7159 | 17.3702 | 259325 | 211328 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LG | SA183LG | sa18 3lg | sa183lg | Carmarthenshire |  | Garnswllt |  | 1581 | Over1500 | 3.1644 | 2.3154 | 1.698 | 29.4674 | 15.7159 | 17.3702 | 259344 | 211548 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LH | SA183LH | sa18 3lh | sa183lh | Carmarthenshire |  | Garnswllt |  | 1596 | Over1500 | 3.1945 | 2.3374 | 1.7141 | 29.7469 | 15.865 | 17.535 | 259787 | 212016 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LL | SA183LL | sa18 3ll | sa183ll | Carmarthenshire |  | Garnswllt |  | 1596 | Over1500 | 3.1945 | 2.3374 | 1.7141 | 29.7469 | 15.865 | 17.535 | 259826 | 212193 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LN | SA183LN | sa18 3ln | sa183ln | Carmarthenshire |  | Garnswllt |  | 1557 | Over1500 | 3.1164 | 2.2803 | 1.6722 | 29.02 | 15.4774 | 17.1065 | 260045 | 212350 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LP | SA183LP | sa18 3lp | sa183lp | Carmarthenshire |  | Garnswllt |  | 1596 | Over1500 | 3.1945 | 2.3374 | 1.7141 | 29.7469 | 15.865 | 17.535 | 259871 | 212275 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LR | SA183LR | sa18 3lr | sa183lr | Carmarthenshire |  | Garnswllt |  | 1581 | Over1500 | 3.1644 | 2.3154 | 1.698 | 29.4674 | 15.7159 | 17.3702 | 259719 | 211960 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LW | SA183LW | sa18 3lw | sa183lw | Carmarthenshire |  | Garnswllt |  | 1557 | Over1500 | 3.1164 | 2.2803 | 1.6722 | 29.02 | 15.4774 | 17.1065 | 260242 | 212541 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LY | SA183LY | sa18 3ly | sa183ly | Carmarthenshire |  | Garnswllt |  | 1559 | Over1500 | 3.1204 | 2.2832 | 1.6744 | 29.0573 | 15.4972 | 17.1285 | 260935 | 213677 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LZ | SA183LZ | sa18 3lz | sa183lz | Carmarthenshire |  | Carmel & Pant-Y-Llyn |  | 1609 | Over1500 | 3.2205 | 2.3564 | 1.7281 | 29.9892 | 15.9943 | 17.6779 | 259017 | 217657 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NA | SA183NA | sa18 3na | sa183na | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261110 | 213549 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NB | SA183NB | sa18 3nb | sa183nb | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261710 | 212987 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3ND | SA183ND | sa18 3nd | sa183nd | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261893 | 213600 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NE | SA183NE | sa18 3ne | sa183ne | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262229 | 213556 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NF | SA183NF | sa18 3nf | sa183nf | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262093 | 213390 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NG | SA183NG | sa18 3ng | sa183ng | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262037 | 214067 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NH | SA183NH | sa18 3nh | sa183nh | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260845 | 210702 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NJ | SA183NJ | sa18 3nj | sa183nj | Carmarthenshire |  | Carmel & Pant-Y-Llyn |  | 1609 | Over1500 | 3.2205 | 2.3564 | 1.7281 | 29.9892 | 15.9943 | 17.6779 | 259681 | 217626 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NL | SA183NL | sa18 3nl | sa183nl | Carmarthenshire |  | Garnswllt |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 262006 | 214533 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NN | SA183NN | sa18 3nn | sa183nn | Carmarthenshire |  | Garnswllt |  | 1581 | Over1500 | 3.1644 | 2.3154 | 1.698 | 29.4674 | 15.7159 | 17.3702 | 259374 | 211382 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NP | SA183NP | sa18 3np | sa183np | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262188 | 213444 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NQ | SA183NQ | sa18 3nq | sa183nq | Carmarthenshire |  | Carmel & Pant-Y-Llyn |  | 1609 | Over1500 | 3.2205 | 2.3564 | 1.7281 | 29.9892 | 15.9943 | 17.6779 | 259589 | 217457 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NR | SA183NR | sa18 3nr | sa183nr | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 262012 | 210808 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NS | SA183NS | sa18 3ns | sa183ns | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261613 | 210701 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NT | SA183NT | sa18 3nt | sa183nt | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261028 | 210749 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NW | SA183NW | sa18 3nw | sa183nw | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260817 | 210561 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NX | SA183NX | sa18 3nx | sa183nx | Carmarthenshire |  | Carmel & Pant-Y-Llyn |  | 1609 | Over1500 | 3.2205 | 2.3564 | 1.7281 | 29.9892 | 15.9943 | 17.6779 | 259548 | 217759 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NY | SA183NY | sa18 3ny | sa183ny | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260700 | 210482 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3NZ | SA183NZ | sa18 3nz | sa183nz | Carmarthenshire |  | Carmel & Pant-Y-Llyn |  | 1609 | Over1500 | 3.2205 | 2.3564 | 1.7281 | 29.9892 | 15.9943 | 17.6779 | 259689 | 217482 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PA | SA183PA | sa18 3pa | sa183pa | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260680 | 210634 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PB | SA183PB | sa18 3pb | sa183pb | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260650 | 210426 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PD | SA183PD | sa18 3pd | sa183pd | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260412 | 210262 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PE | SA183PE | sa18 3pe | sa183pe | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260483 | 210146 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PF | SA183PF | sa18 3pf | sa183pf | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260563 | 210024 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PG | SA183PG | sa18 3pg | sa183pg | Carmarthenshire |  | Garnswllt |  | 1513 | Over1500 | 3.0283 | 2.2158 | 1.625 | 28.1999 | 15.04 | 16.6231 | 261579 | 209663 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PJ | SA183PJ | sa18 3pj | sa183pj | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260521 | 210339 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PL | SA183PL | sa18 3pl | sa183pl | Carmarthenshire |  | Garnswllt |  | 1574 | Over1500 | 3.1504 | 2.3052 | 1.6905 | 29.3369 | 15.6463 | 17.2933 | 260603 | 209533 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PQ | SA183PQ | sa18 3pq | sa183pq | Carmarthenshire |  | Carmel & Pant-Y-Llyn |  | 1568 | Over1500 | 3.1384 | 2.2964 | 1.684 | 29.2251 | 15.5867 | 17.2274 | 260363 | 217098 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PR | SA183PR | sa18 3pr | sa183pr | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261597 | 210514 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PS | SA183PS | sa18 3ps | sa183ps | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261606 | 210435 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PT | SA183PT | sa18 3pt | sa183pt | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261497 | 210555 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PU | SA183PU | sa18 3pu | sa183pu | Carmarthenshire |  | Carmel & Pant-Y-Llyn |  | 1609 | Over1500 | 3.2205 | 2.3564 | 1.7281 | 29.9892 | 15.9943 | 17.6779 | 259718 | 217490 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3PY | SA183PY | sa18 3py | sa183py | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261522 | 210605 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QA | SA183QA | sa18 3qa | sa183qa | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260365 | 210468 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QB | SA183QB | sa18 3qb | sa183qb | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260202 | 210463 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QD | SA183QD | sa18 3qd | sa183qd | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260581 | 210641 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QE | SA183QE | sa18 3qe | sa183qe | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260625 | 210564 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QF | SA183QF | sa18 3qf | sa183qf | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260805 | 210761 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QG | SA183QG | sa18 3qg | sa183qg | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261031 | 210871 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QH | SA183QH | sa18 3qh | sa183qh | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260840 | 210891 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QJ | SA183QJ | sa18 3qj | sa183qj | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260735 | 210903 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QL | SA183QL | sa18 3ql | sa183ql | Carmarthenshire |  | Garnswllt |  | 1547 | Over1500 | 3.0964 | 2.2656 | 1.6615 | 28.8337 | 15.3779 | 16.9967 | 260878 | 211049 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QN | SA183QN | sa18 3qn | sa183qn | Carmarthenshire |  | Garnswllt |  | 1547 | Over1500 | 3.0964 | 2.2656 | 1.6615 | 28.8337 | 15.3779 | 16.9967 | 260827 | 211198 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QP | SA183QP | sa18 3qp | sa183qp | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261494 | 211702 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QQ | SA183QQ | sa18 3qq | sa183qq | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261087 | 210820 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QR | SA183QR | sa18 3qr | sa183qr | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261352 | 211700 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QS | SA183QS | sa18 3qs | sa183qs | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261485 | 211647 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QT | SA183QT | sa18 3qt | sa183qt | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260428 | 210415 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QU | SA183QU | sa18 3qu | sa183qu | Carmarthenshire |  | Garnswllt |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262351 | 213028 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QW | SA183QW | sa18 3qw | sa183qw | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261207 | 211419 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QX | SA183QX | sa18 3qx | sa183qx | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261540 | 211648 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3QZ | SA183QZ | sa18 3qz | sa183qz | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261787 | 211772 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RA | SA183RA | sa18 3ra | sa183ra | Carmarthenshire |  | Garnswllt |  | 1578 | Over1500 | 3.1584 | 2.311 | 1.6948 | 29.4114 | 15.6861 | 17.3373 | 260357 | 210166 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RB | SA183RB | sa18 3rb | sa183rb | Carmarthenshire |  | Garnswllt |  | 1493 | 1200-1500 | 2.9883 | 2.1866 | 1.6035 | 27.8272 | 14.8412 | 16.4034 | 262181 | 211752 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RD | SA183RD | sa18 3rd | sa183rd | Carmarthenshire |  | Garnswllt |  | 1575 | Over1500 | 3.1524 | 2.3067 | 1.6915 | 29.3555 | 15.6563 | 17.3043 | 259550 | 209976 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RE | SA183RE | sa18 3re | sa183re | Carmarthenshire |  | Garnswllt |  | 1575 | Over1500 | 3.1524 | 2.3067 | 1.6915 | 29.3555 | 15.6563 | 17.3043 | 259473 | 209980 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RF | SA183RF | sa18 3rf | sa183rf | Carmarthenshire |  | Garnswllt |  | 1608 | Over1500 | 3.2185 | 2.355 | 1.727 | 29.9706 | 15.9843 | 17.6669 | 259169 | 209767 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RJ | SA183RJ | sa18 3rj | sa183rj | Carmarthenshire |  | Cwmgwili |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258790 | 211296 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RJ | SA183RJ | sa18 3rj | sa183rj | Carmarthenshire |  | Garnswllt |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258790 | 211296 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RL | SA183RL | sa18 3rl | sa183rl | Carmarthenshire |  | Cwmgwili |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 257772 | 209750 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RP | SA183RP | sa18 3rp | sa183rp | Carmarthenshire |  | Cwmgwili |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258750 | 211180 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RP | SA183RP | sa18 3rp | sa183rp | Carmarthenshire |  | Garnswllt |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258750 | 211180 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RQ | SA183RQ | sa18 3rq | sa183rq | Carmarthenshire |  | Garnswllt |  | 1581 | Over1500 | 3.1644 | 2.3154 | 1.698 | 29.4674 | 15.7159 | 17.3702 | 259116 | 211348 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RS | SA183RS | sa18 3rs | sa183rs | Carmarthenshire |  | Garnswllt |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258970 | 211012 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RT | SA183RT | sa18 3rt | sa183rt | Carmarthenshire |  | Cwmgwili |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258664 | 211489 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RT | SA183RT | sa18 3rt | sa183rt | Carmarthenshire |  | Garnswllt |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258664 | 211489 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RU | SA183RU | sa18 3ru | sa183ru | Carmarthenshire |  | Garnswllt |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258815 | 211562 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RX | SA183RX | sa18 3rx | sa183rx | Carmarthenshire |  | Garnswllt |  | 1581 | Over1500 | 3.1644 | 2.3154 | 1.698 | 29.4674 | 15.7159 | 17.3702 | 259059 | 211319 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3RY | SA183RY | sa18 3ry | sa183ry | Carmarthenshire |  | Garnswllt |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258725 | 211778 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SA | SA183SA | sa18 3sa | sa183sa | Carmarthenshire |  | Garnswllt |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258637 | 211765 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SB | SA183SB | sa18 3sb | sa183sb | Carmarthenshire |  | Garnswllt |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258798 | 211922 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SD | SA183SD | sa18 3sd | sa183sd | Carmarthenshire |  | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258604 | 212017 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SE | SA183SE | sa18 3se | sa183se | Carmarthenshire |  | Garnswllt |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258951 | 211809 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SF | SA183SF | sa18 3sf | sa183sf | Carmarthenshire |  | Garnswllt |  | 1581 | Over1500 | 3.1644 | 2.3154 | 1.698 | 29.4674 | 15.7159 | 17.3702 | 259057 | 211460 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SG | SA183SG | sa18 3sg | sa183sg | Carmarthenshire |  | Garnswllt |  | 1581 | Over1500 | 3.1644 | 2.3154 | 1.698 | 29.4674 | 15.7159 | 17.3702 | 259209 | 211489 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SJ | SA183SJ | sa18 3sj | sa183sj | Carmarthenshire |  | Garnswllt |  | 1581 | Over1500 | 3.1644 | 2.3154 | 1.698 | 29.4674 | 15.7159 | 17.3702 | 259204 | 211050 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SL | SA183SL | sa18 3sl | sa183sl | Carmarthenshire |  | Garnswllt |  | 1575 | Over1500 | 3.1524 | 2.3067 | 1.6915 | 29.3555 | 15.6563 | 17.3043 | 259441 | 210358 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SN | SA183SN | sa18 3sn | sa183sn | Carmarthenshire |  | Garnswllt |  | 1575 | Over1500 | 3.1524 | 2.3067 | 1.6915 | 29.3555 | 15.6563 | 17.3043 | 259435 | 210055 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SP | SA183SP | sa18 3sp | sa183sp | Carmarthenshire |  | Garnswllt |  | 1574 | Over1500 | 3.1504 | 2.3052 | 1.6905 | 29.3369 | 15.6463 | 17.2933 | 260507 | 209947 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SR | SA183SR | sa18 3sr | sa183sr | Carmarthenshire |  | Cwmgwili |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258737 | 211457 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SR | SA183SR | sa18 3sr | sa183sr | Carmarthenshire |  | Garnswllt |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258737 | 211457 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SS | SA183SS | sa18 3ss | sa183ss | Carmarthenshire |  | Cwmgwili |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258903 | 211471 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SS | SA183SS | sa18 3ss | sa183ss | Carmarthenshire |  | Garnswllt |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258903 | 211471 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SU | SA183SU | sa18 3su | sa183su | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262361 | 212835 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SW | SA183SW | sa18 3sw | sa183sw | Carmarthenshire |  | Garnswllt |  | 1574 | Over1500 | 3.1504 | 2.3052 | 1.6905 | 29.3369 | 15.6463 | 17.2933 | 260256 | 209939 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SX | SA183SX | sa18 3sx | sa183sx | Carmarthenshire |  | Garnswllt |  | 1637 | Over1500 | 3.2765 | 2.3975 | 1.7581 | 30.5111 | 16.2726 | 17.9855 | 258900 | 211977 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SY | SA183SY | sa18 3sy | sa183sy | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262355 | 212721 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3SZ | SA183SZ | sa18 3sz | sa183sz | Carmarthenshire |  | Garnswllt |  | 1557 | Over1500 | 3.1164 | 2.2803 | 1.6722 | 29.02 | 15.4774 | 17.1065 | 260190 | 212281 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TA | SA183TA | sa18 3ta | sa183ta | Carmarthenshire |  | Garnswllt |  | 1490 | 1200-1500 | 2.9823 | 2.1822 | 1.6003 | 27.7713 | 14.8113 | 16.3704 | 262201 | 212672 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TB | SA183TB | sa18 3tb | sa183tb | Carmarthenshire |  | Garnswllt |  | 1520 | Over1500 | 3.0423 | 2.2261 | 1.6325 | 28.3304 | 15.1096 | 16.7 | 261622 | 212496 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TD | SA183TD | sa18 3td | sa183td | Carmarthenshire |  | Garnswllt |  | 1520 | Over1500 | 3.0423 | 2.2261 | 1.6325 | 28.3304 | 15.1096 | 16.7 | 261571 | 212302 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TE | SA183TE | sa18 3te | sa183te | Carmarthenshire |  | Garnswllt |  | 1520 | Over1500 | 3.0423 | 2.2261 | 1.6325 | 28.3304 | 15.1096 | 16.7 | 261782 | 212103 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TF | SA183TF | sa18 3tf | sa183tf | Carmarthenshire |  | Garnswllt |  | 1520 | Over1500 | 3.0423 | 2.2261 | 1.6325 | 28.3304 | 15.1096 | 16.7 | 261729 | 212010 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TG | SA183TG | sa18 3tg | sa183tg | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261791 | 211916 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TH | SA183TH | sa18 3th | sa183th | Carmarthenshire |  | Garnswllt |  | 1520 | Over1500 | 3.0423 | 2.2261 | 1.6325 | 28.3304 | 15.1096 | 16.7 | 261280 | 212530 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TJ | SA183TJ | sa18 3tj | sa183tj | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261706 | 211906 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TL | SA183TL | sa18 3tl | sa183tl | Carmarthenshire |  | Garnswllt |  | 1520 | Over1500 | 3.0423 | 2.2261 | 1.6325 | 28.3304 | 15.1096 | 16.7 | 261354 | 212588 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TN | SA183TN | sa18 3tn | sa183tn | Carmarthenshire |  | Garnswllt |  | 1557 | Over1500 | 3.1164 | 2.2803 | 1.6722 | 29.02 | 15.4774 | 17.1065 | 260579 | 212468 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TP | SA183TP | sa18 3tp | sa183tp | Carmarthenshire |  | Garnswllt |  | 1557 | Over1500 | 3.1164 | 2.2803 | 1.6722 | 29.02 | 15.4774 | 17.1065 | 260302 | 212201 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TQ | SA183TQ | sa18 3tq | sa183tq | Carmarthenshire |  | Garnswllt |  | 1520 | Over1500 | 3.0423 | 2.2261 | 1.6325 | 28.3304 | 15.1096 | 16.7 | 261681 | 212233 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TR | SA183TR | sa18 3tr | sa183tr | Carmarthenshire |  | Garnswllt |  | 1520 | Over1500 | 3.0423 | 2.2261 | 1.6325 | 28.3304 | 15.1096 | 16.7 | 261581 | 212566 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TS | SA183TS | sa18 3ts | sa183ts | Carmarthenshire |  | Garnswllt |  | 1520 | Over1500 | 3.0423 | 2.2261 | 1.6325 | 28.3304 | 15.1096 | 16.7 | 261528 | 212619 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TT | SA183TT | sa18 3tt | sa183tt | Carmarthenshire |  | Cwmgwili |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258931 | 211417 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TT | SA183TT | sa18 3tt | sa183tt | Carmarthenshire |  | Garnswllt |  | 1602 | Over1500 | 3.2065 | 2.3462 | 1.7205 | 29.8588 | 15.9247 | 17.601 | 258931 | 211417 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TU | SA183TU | sa18 3tu | sa183tu | Carmarthenshire |  | Garnswllt |  | 1547 | Over1500 | 3.0964 | 2.2656 | 1.6615 | 28.8337 | 15.3779 | 16.9967 | 260614 | 211463 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TW | SA183TW | sa18 3tw | sa183tw | Carmarthenshire |  | Garnswllt |  | 1557 | Over1500 | 3.1164 | 2.2803 | 1.6722 | 29.02 | 15.4774 | 17.1065 | 260746 | 212417 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TX | SA183TX | sa18 3tx | sa183tx | Carmarthenshire |  | Garnswllt |  | 1520 | Over1500 | 3.0423 | 2.2261 | 1.6325 | 28.3304 | 15.1096 | 16.7 | 261695 | 212318 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TY | SA183TY | sa18 3ty | sa183ty | Carmarthenshire |  | Garnswllt |  | 1557 | Over1500 | 3.1164 | 2.2803 | 1.6722 | 29.02 | 15.4774 | 17.1065 | 260294 | 212504 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3TZ | SA183TZ | sa18 3tz | sa183tz | Carmarthenshire |  | Garnswllt |  | 1557 | Over1500 | 3.1164 | 2.2803 | 1.6722 | 29.02 | 15.4774 | 17.1065 | 260256 | 212337 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UA | SA183UA | sa18 3ua | sa183ua | Carmarthenshire |  | Garnswllt |  | 1547 | Over1500 | 3.0964 | 2.2656 | 1.6615 | 28.8337 | 15.3779 | 16.9967 | 260616 | 211391 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UB | SA183UB | sa18 3ub | sa183ub | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261089 | 211480 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UE | SA183UE | sa18 3ue | sa183ue | Carmarthenshire |  | Garnswllt |  | 1519 | Over1500 | 3.0403 | 2.2246 | 1.6314 | 28.3118 | 15.0996 | 16.689 | 261125 | 211650 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UF | SA183UF | sa18 3uf | sa183uf | Carmarthenshire |  | Garnswllt |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 261748 | 214607 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UG | SA183UG | sa18 3ug | sa183ug | Carmarthenshire |  | Garnswllt |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 261758 | 214704 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UH | SA183UH | sa18 3uh | sa183uh | Carmarthenshire |  | Garnswllt |  | 1547 | Over1500 | 3.0964 | 2.2656 | 1.6615 | 28.8337 | 15.3779 | 16.9967 | 260720 | 211181 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UJ | SA183UJ | sa18 3uj | sa183uj | Carmarthenshire |  | Garnswllt |  | 1608 | Over1500 | 3.2185 | 2.355 | 1.727 | 29.9706 | 15.9843 | 17.6669 | 259381 | 209951 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UL | SA183UL | sa18 3ul | sa183ul | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261916 | 215448 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UP | SA183UP | sa18 3up | sa183up | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261884 | 215399 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UR | SA183UR | sa18 3ur | sa183ur | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261730 | 215161 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3US | SA183US | sa18 3us | sa183us | Carmarthenshire |  | Garnswllt |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 261624 | 214835 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UT | SA183UT | sa18 3ut | sa183ut | Carmarthenshire |  | Garnswllt |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 261578 | 214786 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UU | SA183UU | sa18 3uu | sa183uu | Carmarthenshire |  | Garnswllt |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 261701 | 214788 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UW | SA183UW | sa18 3uw | sa183uw | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261843 | 215318 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3UY | SA183UY | sa18 3uy | sa183uy | Carmarthenshire |  | Garnswllt |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 261740 | 214941 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YA | SA183YA | sa18 3ya | sa183ya | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261939 | 214993 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YB | SA183YB | sa18 3yb | sa183yb | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261960 | 215031 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YD | SA183YD | sa18 3yd | sa183yd | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261927 | 215111 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YF | SA183YF | sa18 3yf | sa183yf | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 262002 | 215166 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YG | SA183YG | sa18 3yg | sa183yg | Carmarthenshire |  | Garnswllt |  | 1517 | Over1500 | 3.0363 | 2.2217 | 1.6293 | 28.2745 | 15.0797 | 16.6671 | 262058 | 215020 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YH | SA183YH | sa18 3yh | sa183yh | Carmarthenshire |  | Garnswllt |  | 1521 | Over1500 | 3.0443 | 2.2276 | 1.6335 | 28.3491 | 15.1195 | 16.711 | 262085 | 214923 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YL | SA183YL | sa18 3yl | sa183yl | Carmarthenshire |  | Garnswllt |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 261991 | 214927 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YN | SA183YN | sa18 3yn | sa183yn | Carmarthenshire |  | Garnswllt |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 261612 | 214960 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YP | SA183YP | sa18 3yp | sa183yp | Carmarthenshire |  | Garnswllt |  | 1524 | Over1500 | 3.0503 | 2.232 | 1.6368 | 28.405 | 15.1493 | 16.744 | 261991 | 214843 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YR | SA183YR | sa18 3yr | sa183yr | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261697 | 215252 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YS | SA183YS | sa18 3ys | sa183ys | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261469 | 215115 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YT | SA183YT | sa18 3yt | sa183yt | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261612 | 215073 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3YU | SA183YU | sa18 3yu | sa183yu | Carmarthenshire |  | Garnswllt |  | 1528 | Over1500 | 3.0584 | 2.2378 | 1.6411 | 28.4795 | 15.1891 | 16.7879 | 261625 | 214995 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8NB | SA328NB | sa32 8nb | sa328nb | Carmarthenshire |  | Carmel & Pant-Y-Llyn |  | 1715 | Over1500 | 3.4326 | 2.5117 | 1.8419 | 31.9649 | 17.048 | 18.8425 | 257890 | 217812 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0AA | SA40AA | sa4 0aa | sa40aa | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257522 | 203722 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0AB | SA40AB | sa4 0ab | sa40ab | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257519 | 203719 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0AD | SA40AD | sa4 0ad | sa40ad | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258301 | 204084 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0FB | SA40FB | sa4 0fb | sa40fb | Carmarthenshire |  | Llanedi |  | 1597 | Over1500 | 3.1965 | 2.3389 | 1.7152 | 29.7656 | 15.875 | 17.546 | 258532 | 208178 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0FE | SA40FE | sa4 0fe | sa40fe | Carmarthenshire |  | Llanedi |  | 1597 | Over1500 | 3.1965 | 2.3389 | 1.7152 | 29.7656 | 15.875 | 17.546 | 258602 | 208727 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0FF | SA40FF | sa4 0ff | sa40ff | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257652 | 203501 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0FG | SA40FG | sa4 0fg | sa40fg | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257586 | 203588 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0FW | SA40FW | sa4 0fw | sa40fw | Carmarthenshire |  | Llannant |  | 1391 | 1200-1500 | 2.7841 | 2.0372 | 1.4939 | 25.9261 | 13.8272 | 15.2827 | 257614 | 203976 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TF | SA40TF | sa4 0tf | sa40tf | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258024 | 203832 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TG | SA40TG | sa4 0tg | sa40tg | Carmarthenshire |  | Llannant |  | 1391 | 1200-1500 | 2.7841 | 2.0372 | 1.4939 | 25.9261 | 13.8272 | 15.2827 | 257937 | 204886 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TJ | SA40TJ | sa4 0tj | sa40tj | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258575 | 203922 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TN | SA40TN | sa4 0tn | sa40tn | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258673 | 204061 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TP | SA40TP | sa4 0tp | sa40tp | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258037 | 203635 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TQ | SA40TQ | sa4 0tq | sa40tq | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258290 | 204605 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TS | SA40TS | sa4 0ts | sa40ts | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258207 | 204693 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TT | SA40TT | sa4 0tt | sa40tt | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258098 | 204896 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TU | SA40TU | sa4 0tu | sa40tu | Carmarthenshire |  | Llannant |  | 1391 | 1200-1500 | 2.7841 | 2.0372 | 1.4939 | 25.9261 | 13.8272 | 15.2827 | 257919 | 204774 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TW | SA40TW | sa4 0tw | sa40tw | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258385 | 204433 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TX | SA40TX | sa4 0tx | sa40tx | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258110 | 204574 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TY | SA40TY | sa4 0ty | sa40ty | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258071 | 204694 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0TZ | SA40TZ | sa4 0tz | sa40tz | Carmarthenshire |  | Llannant |  | 1391 | 1200-1500 | 2.7841 | 2.0372 | 1.4939 | 25.9261 | 13.8272 | 15.2827 | 257920 | 204858 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UA | SA40UA | sa4 0ua | sa40ua | Carmarthenshire |  | Llannant |  | 1391 | 1200-1500 | 2.7841 | 2.0372 | 1.4939 | 25.9261 | 13.8272 | 15.2827 | 257970 | 204592 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UB | SA40UB | sa4 0ub | sa40ub | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258221 | 204337 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UD | SA40UD | sa4 0ud | sa40ud | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258235 | 203978 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UE | SA40UE | sa4 0ue | sa40ue | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258304 | 204214 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UG | SA40UG | sa4 0ug | sa40ug | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258457 | 204107 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UH | SA40UH | sa4 0uh | sa40uh | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258342 | 204312 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UJ | SA40UJ | sa4 0uj | sa40uj | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258402 | 204219 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UL | SA40UL | sa4 0ul | sa40ul | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258613 | 203925 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UN | SA40UN | sa4 0un | sa40un | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258626 | 203876 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UP | SA40UP | sa4 0up | sa40up | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258270 | 203713 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UQ | SA40UQ | sa4 0uq | sa40uq | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258172 | 203751 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UR | SA40UR | sa4 0ur | sa40ur | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258452 | 203667 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0US | SA40US | sa4 0us | sa40us | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258483 | 203914 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UT | SA40UT | sa4 0ut | sa40ut | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258369 | 203637 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UU | SA40UU | sa4 0uu | sa40uu | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258142 | 203670 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UW | SA40UW | sa4 0uw | sa40uw | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258448 | 203787 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UX | SA40UX | sa4 0ux | sa40ux | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258058 | 203514 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UY | SA40UY | sa4 0uy | sa40uy | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258104 | 203758 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0UZ | SA40UZ | sa4 0uz | sa40uz | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258058 | 203735 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XA | SA40XA | sa4 0xa | sa40xa | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257976 | 203569 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XB | SA40XB | sa4 0xb | sa40xb | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257873 | 203390 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XD | SA40XD | sa4 0xd | sa40xd | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258454 | 203727 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XE | SA40XE | sa4 0xe | sa40xe | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257870 | 203574 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XF | SA40XF | sa4 0xf | sa40xf | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257809 | 203793 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XG | SA40XG | sa4 0xg | sa40xg | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257754 | 203734 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XH | SA40XH | sa4 0xh | sa40xh | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257749 | 203298 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XJ | SA40XJ | sa4 0xj | sa40xj | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257652 | 203759 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XL | SA40XL | sa4 0xl | sa40xl | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257623 | 203694 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XN | SA40XN | sa4 0xn | sa40xn | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257716 | 203467 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XP | SA40XP | sa4 0xp | sa40xp | Carmarthenshire |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258233 | 203503 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XQ | SA40XQ | sa4 0xq | sa40xq | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257721 | 203748 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XR | SA40XR | sa4 0xr | sa40xr | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257802 | 203485 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XS | SA40XS | sa4 0xs | sa40xs | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258506 | 204056 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XT | SA40XT | sa4 0xt | sa40xt | Carmarthenshire |  | Llannant |  | 1372 | 1200-1500 | 2.7461 | 2.0093 | 1.4735 | 25.5719 | 13.6384 | 15.074 | 257872 | 203306 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XW | SA40XW | sa4 0xw | sa40xw | Carmarthenshire |  | Llanedi |  | 1570 | Over1500 | 3.1424 | 2.2993 | 1.6862 | 29.2623 | 15.6066 | 17.2494 | 258707 | 207120 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XX | SA40XX | sa4 0xx | sa40xx | Carmarthenshire |  | Llannant |  | 1391 | 1200-1500 | 2.7841 | 2.0372 | 1.4939 | 25.9261 | 13.8272 | 15.2827 | 257584 | 204177 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0XZ | SA40XZ | sa4 0xz | sa40xz | Carmarthenshire |  | Llannant |  | 1391 | 1200-1500 | 2.7841 | 2.0372 | 1.4939 | 25.9261 | 13.8272 | 15.2827 | 257429 | 204334 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0YJ | SA40YJ | sa4 0yj | sa40yj | Carmarthenshire |  | Llannant |  | 1391 | 1200-1500 | 2.7841 | 2.0372 | 1.4939 | 25.9261 | 13.8272 | 15.2827 | 257788 | 204393 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0YP | SA40YP | sa4 0yp | sa40yp | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258178 | 204900 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0YS | SA40YS | sa4 0ys | sa40ys | Carmarthenshire |  | Llanedi |  | 1544 | Over1500 | 3.0904 | 2.2612 | 1.6582 | 28.7777 | 15.3481 | 16.9637 | 258718 | 206853 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0YT | SA40YT | sa4 0yt | sa40yt | Carmarthenshire |  | Llanedi |  | 1570 | Over1500 | 3.1424 | 2.2993 | 1.6862 | 29.2623 | 15.6066 | 17.2494 | 258608 | 207189 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0YU | SA40YU | sa4 0yu | sa40yu | Carmarthenshire |  | Llanedi |  | 1570 | Over1500 | 3.1424 | 2.2993 | 1.6862 | 29.2623 | 15.6066 | 17.2494 | 258997 | 207173 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0YW | SA40YW | sa4 0yw | sa40yw | Carmarthenshire |  | Llannant |  | 1412 | 1200-1500 | 2.8262 | 2.0679 | 1.5165 | 26.3175 | 14.036 | 15.5135 | 258194 | 205189 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0YY | SA40YY | sa4 0yy | sa40yy | Carmarthenshire |  | Llanedi |  | 1544 | Over1500 | 3.0904 | 2.2612 | 1.6582 | 28.7777 | 15.3481 | 16.9637 | 258639 | 206853 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0YZ | SA40YZ | sa4 0yz | sa40yz | Carmarthenshire |  | Llanedi |  | 1570 | Over1500 | 3.1424 | 2.2993 | 1.6862 | 29.2623 | 15.6066 | 17.2494 | 258699 | 207211 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0ZE | SA40ZE | sa4 0ze | sa40ze | Carmarthenshire |  | Llannant |  | 1412 | 1200-1500 | 2.8262 | 2.0679 | 1.5165 | 26.3175 | 14.036 | 15.5135 | 258187 | 205051 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0ZL | SA40ZL | sa4 0zl | sa40zl | Carmarthenshire |  | Llanedi |  | 1570 | Over1500 | 3.1424 | 2.2993 | 1.6862 | 29.2623 | 15.6066 | 17.2494 | 258568 | 207010 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0ZN | SA40ZN | sa4 0zn | sa40zn | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258019 | 204627 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 0ZW | SA40ZW | sa4 0zw | sa40zw | Carmarthenshire |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258150 | 204235 | Carmarthenshire LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA4 4AB | SA44AB | sa4 4ab | sa44ab | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258463 | 199190 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4AU | SA44AU | sa4 4au | sa44au | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257740 | 198900 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4AW | SA44AW | sa4 4aw | sa44aw | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258403 | 199302 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4BA | SA44BA | sa4 4ba | sa44ba | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257907 | 199510 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4BB | SA44BB | sa4 4bb | sa44bb | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257961 | 199487 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4BD | SA44BD | sa4 4bd | sa44bd | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257908 | 199411 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4BF | SA44BF | sa4 4bf | sa44bf | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257784 | 199215 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4BQ | SA44BQ | sa4 4bq | sa44bq | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258337 | 198344 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4DH | SA44DH | sa4 4dh | sa44dh | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258482 | 199723 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4FA | SA44FA | sa4 4fa | sa44fa | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258075 | 199239 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4FB | SA44FB | sa4 4fb | sa44fb | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258016 | 199121 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4FD | SA44FD | sa4 4fd | sa44fd | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257888 | 199099 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4FH | SA44FH | sa4 4fh | sa44fh | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258824 | 199752 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4FS | SA44FS | sa4 4fs | sa44fs | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258644 | 199119 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4FT | SA44FT | sa4 4ft | sa44ft | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258547 | 199147 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4FU | SA44FU | sa4 4fu | sa44fu | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258475 | 199383 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4FX | SA44FX | sa4 4fx | sa44fx | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258564 | 199541 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4FY | SA44FY | sa4 4fy | sa44fy | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258408 | 199811 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4FZ | SA44FZ | sa4 4fz | sa44fz | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258351 | 199747 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GA | SA44GA | sa4 4ga | sa44ga | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258342 | 199662 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GB | SA44GB | sa4 4gb | sa44gb | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258131 | 199656 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GD | SA44GD | sa4 4gd | sa44gd | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258180 | 199850 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GE | SA44GE | sa4 4ge | sa44ge | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258602 | 199746 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GF | SA44GF | sa4 4gf | sa44gf | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258630 | 199681 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GH | SA44GH | sa4 4gh | sa44gh | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258685 | 199695 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GJ | SA44GJ | sa4 4gj | sa44gj | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258016 | 199606 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GL | SA44GL | sa4 4gl | sa44gl | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257900 | 199617 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GN | SA44GN | sa4 4gn | sa44gn | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257935 | 199051 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GP | SA44GP | sa4 4gp | sa44gp | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259122 | 200098 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GQ | SA44GQ | sa4 4gq | sa44gq | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258656 | 199565 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GR | SA44GR | sa4 4gr | sa44gr | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259139 | 200497 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GS | SA44GS | sa4 4gs | sa44gs | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259114 | 200508 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GT | SA44GT | sa4 4gt | sa44gt | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259125 | 200763 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GU | SA44GU | sa4 4gu | sa44gu | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259152 | 200768 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GW | SA44GW | sa4 4gw | sa44gw | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257975 | 199099 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GX | SA44GX | sa4 4gx | sa44gx | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257886 | 199586 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GY | SA44GY | sa4 4gy | sa44gy | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259401 | 200911 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4GZ | SA44GZ | sa4 4gz | sa44gz | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259248 | 200500 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4HB | SA44HB | sa4 4hb | sa44hb | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257989 | 199652 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4HH | SA44HH | sa4 4hh | sa44hh | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258657 | 199299 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4HP | SA44HP | sa4 4hp | sa44hp | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258615 | 199343 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4HX | SA44HX | sa4 4hx | sa44hx | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258945 | 199865 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4JG | SA44JG | sa4 4jg | sa44jg | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257829 | 198962 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4JL | SA44JL | sa4 4jl | sa44jl | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258516 | 199594 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4JN | SA44JN | sa4 4jn | sa44jn | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258500 | 199656 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4JP | SA44JP | sa4 4jp | sa44jp | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258556 | 199619 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4JW | SA44JW | sa4 4jw | sa44jw | Swansea |  | Llannant |  | 1336 | 1200-1500 | 2.6741 | 1.9566 | 1.4349 | 24.9009 | 13.2805 | 14.6785 | 259296 | 200992 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4JY | SA44JY | sa4 4jy | sa44jy | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257786 | 199021 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4JZ | SA44JZ | sa4 4jz | sa44jz | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257848 | 199101 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4LJ | SA44LJ | sa4 4lj | sa44lj | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258725 | 199716 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4LR | SA44LR | sa4 4lr | sa44lr | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258867 | 199583 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4LS | SA44LS | sa4 4ls | sa44ls | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258973 | 199663 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4LU | SA44LU | sa4 4lu | sa44lu | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258879 | 199684 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4LY | SA44LY | sa4 4ly | sa44ly | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258754 | 199650 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4LZ | SA44LZ | sa4 4lz | sa44lz | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258950 | 199776 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4NA | SA44NA | sa4 4na | sa44na | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258782 | 199798 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4NB | SA44NB | sa4 4nb | sa44nb | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258146 | 199744 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4ND | SA44ND | sa4 4nd | sa44nd | Swansea |  | Llangennech |  | 1289 | 1200-1500 | 2.58 | 1.8878 | 1.3844 | 24.0249 | 12.8133 | 14.1621 | 257655 | 200185 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4ND | SA44ND | sa4 4nd | sa44nd | Swansea |  | Llannant |  | 1289 | 1200-1500 | 2.58 | 1.8878 | 1.3844 | 24.0249 | 12.8133 | 14.1621 | 257655 | 200185 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4NF | SA44NF | sa4 4nf | sa44nf | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258040 | 199737 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4NX | SA44NX | sa4 4nx | sa44nx | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258433 | 198631 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4NY | SA44NY | sa4 4ny | sa44ny | Swansea |  | Llannant |  | 1358 | 1200-1500 | 2.7181 | 1.9888 | 1.4585 | 25.311 | 13.4992 | 14.9202 | 259468 | 199663 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4PA | SA44PA | sa4 4pa | sa44pa | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258424 | 198468 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4PB | SA44PB | sa4 4pb | sa44pb | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258113 | 198460 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4PD | SA44PD | sa4 4pd | sa44pd | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258118 | 198605 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4PE | SA44PE | sa4 4pe | sa44pe | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258203 | 198567 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4PF | SA44PF | sa4 4pf | sa44pf | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258070 | 198579 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4PQ | SA44PQ | sa4 4pq | sa44pq | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258077 | 198478 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4UA | SA44UA | sa4 4ua | sa44ua | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258418 | 198715 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4US | SA44US | sa4 4us | sa44us | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258643 | 198862 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4UU | SA44UU | sa4 4uu | sa44uu | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258478 | 199025 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4UX | SA44UX | sa4 4ux | sa44ux | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258394 | 198803 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4UY | SA44UY | sa4 4uy | sa44uy | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258272 | 198654 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4UZ | SA44UZ | sa4 4uz | sa44uz | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258311 | 198868 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4WB | SA44WB | sa4 4wb | sa44wb | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259359 | 200741 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4WD | SA44WD | sa4 4wd | sa44wd | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259631 | 200903 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4WE | SA44WE | sa4 4we | sa44we | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259258 | 200814 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4WF | SA44WF | sa4 4wf | sa44wf | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259295 | 200681 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4WG | SA44WG | sa4 4wg | sa44wg | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259336 | 200594 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4WL | SA44WL | sa4 4wl | sa44wl | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259229 | 200684 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4WN | SA44WN | sa4 4wn | sa44wn | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259207 | 200461 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4WP | SA44WP | sa4 4wp | sa44wp | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259409 | 200651 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4WQ | SA44WQ | sa4 4wq | sa44wq | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259322 | 200557 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4WR | SA44WR | sa4 4wr | sa44wr | Swansea |  | Llannant |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 259470 | 200625 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XA | SA44XA | sa4 4xa | sa44xa | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258211 | 198778 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XB | SA44XB | sa4 4xb | sa44xb | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258151 | 198790 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XD | SA44XD | sa4 4xd | sa44xd | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258166 | 198662 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XE | SA44XE | sa4 4xe | sa44xe | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258117 | 198650 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XG | SA44XG | sa4 4xg | sa44xg | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258210 | 198907 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XH | SA44XH | sa4 4xh | sa44xh | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258267 | 199062 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XJ | SA44XJ | sa4 4xj | sa44xj | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258347 | 199107 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XL | SA44XL | sa4 4xl | sa44xl | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258347 | 199299 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XN | SA44XN | sa4 4xn | sa44xn | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258346 | 199188 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XP | SA44XP | sa4 4xp | sa44xp | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258374 | 198979 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XQ | SA44XQ | sa4 4xq | sa44xq | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258346 | 198908 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XT | SA44XT | sa4 4xt | sa44xt | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258051 | 199015 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XW | SA44XW | sa4 4xw | sa44xw | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258303 | 199163 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XY | SA44XY | sa4 4xy | sa44xy | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 258012 | 198704 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4XZ | SA44XZ | sa4 4xz | sa44xz | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258084 | 198886 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YA | SA44YA | sa4 4ya | sa44ya | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257970 | 198929 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YB | SA44YB | sa4 4yb | sa44yb | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258201 | 198996 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YD | SA44YD | sa4 4yd | sa44yd | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258069 | 198650 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YE | SA44YE | sa4 4ye | sa44ye | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258172 | 199126 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YF | SA44YF | sa4 4yf | sa44yf | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258017 | 199191 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YG | SA44YG | sa4 4yg | sa44yg | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258335 | 199355 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YH | SA44YH | sa4 4yh | sa44yh | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257922 | 199281 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YJ | SA44YJ | sa4 4yj | sa44yj | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258177 | 199277 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YL | SA44YL | sa4 4yl | sa44yl | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258126 | 199276 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YN | SA44YN | sa4 4yn | sa44yn | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258286 | 199462 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YP | SA44YP | sa4 4yp | sa44yp | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258274 | 199624 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YQ | SA44YQ | sa4 4yq | sa44yq | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258360 | 199327 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YR | SA44YR | sa4 4yr | sa44yr | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258166 | 199544 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YS | SA44YS | sa4 4ys | sa44ys | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258238 | 199528 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YT | SA44YT | sa4 4yt | sa44yt | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258214 | 199325 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YU | SA44YU | sa4 4yu | sa44yu | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258090 | 199463 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YW | SA44YW | sa4 4yw | sa44yw | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258267 | 199403 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YX | SA44YX | sa4 4yx | sa44yx | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258091 | 199332 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YY | SA44YY | sa4 4yy | sa44yy | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257966 | 198833 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4YZ | SA44YZ | sa4 4yz | sa44yz | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257973 | 199268 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4ZA | SA44ZA | sa4 4za | sa44za | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257807 | 198806 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4ZB | SA44ZB | sa4 4zb | sa44zb | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257873 | 198664 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4ZD | SA44ZD | sa4 4zd | sa44zd | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257956 | 198752 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4ZE | SA44ZE | sa4 4ze | sa44ze | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257908 | 198780 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4ZF | SA44ZF | sa4 4zf | sa44zf | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257795 | 198689 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4ZG | SA44ZG | sa4 4zg | sa44zg | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257840 | 198822 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 4ZQ | SA44ZQ | sa4 4zq | sa44zq | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257722 | 198725 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6AG | SA46AG | sa4 6ag | sa46ag | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257609 | 197976 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6AH | SA46AH | sa4 6ah | sa46ah | Swansea |  | Llannant |  | 1341 | 1200-1500 | 2.6841 | 1.9639 | 1.4402 | 24.9941 | 13.3302 | 14.7334 | 257613 | 197915 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6AJ | SA46AJ | sa4 6aj | sa46aj | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257634 | 198046 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6AL | SA46AL | sa4 6al | sa46al | Swansea |  | Llannant |  | 1341 | 1200-1500 | 2.6841 | 1.9639 | 1.4402 | 24.9941 | 13.3302 | 14.7334 | 257728 | 197939 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6BE | SA46BE | sa4 6be | sa46be | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258226 | 198336 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6BG | SA46BG | sa4 6bg | sa46bg | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258346 | 198403 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6JS | SA46JS | sa4 6js | sa46js | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257383 | 198199 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6JU | SA46JU | sa4 6ju | sa46ju | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257522 | 198189 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6JX | SA46JX | sa4 6jx | sa46jx | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257570 | 198269 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6PG | SA46PG | sa4 6pg | sa46pg | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 258004 | 198471 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6PH | SA46PH | sa4 6ph | sa46ph | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257841 | 198438 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6PJ | SA46PJ | sa4 6pj | sa46pj | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257934 | 198467 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6PN | SA46PN | sa4 6pn | sa46pn | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257781 | 198447 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6PP | SA46PP | sa4 6pp | sa46pp | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258044 | 198303 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6PR | SA46PR | sa4 6pr | sa46pr | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257957 | 198231 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6PS | SA46PS | sa4 6ps | sa46ps | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257886 | 198149 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6PW | SA46PW | sa4 6pw | sa46pw | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257746 | 198345 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6PY | SA46PY | sa4 6py | sa46py | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258106 | 199131 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6PZ | SA46PZ | sa4 6pz | sa46pz | Swansea |  | Llannant |  | 1378 | 1200-1500 | 2.7581 | 2.0181 | 1.48 | 25.6838 | 13.698 | 15.1399 | 258061 | 199069 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6QB | SA46QB | sa4 6qb | sa46qb | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257630 | 198324 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6QD | SA46QD | sa4 6qd | sa46qd | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257850 | 198046 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6QF | SA46QF | sa4 6qf | sa46qf | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257782 | 198183 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6QH | SA46QH | sa4 6qh | sa46qh | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257809 | 197977 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6QJ | SA46QJ | sa4 6qj | sa46qj | Swansea |  | Llannant |  | 1341 | 1200-1500 | 2.6841 | 1.9639 | 1.4402 | 24.9941 | 13.3302 | 14.7334 | 257862 | 197957 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6QL | SA46QL | sa4 6ql | sa46ql | Swansea |  | Llannant |  | 1341 | 1200-1500 | 2.6841 | 1.9639 | 1.4402 | 24.9941 | 13.3302 | 14.7334 | 257846 | 197895 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6QP | SA46QP | sa4 6qp | sa46qp | Swansea |  | Llannant |  | 1341 | 1200-1500 | 2.6841 | 1.9639 | 1.4402 | 24.9941 | 13.3302 | 14.7334 | 257924 | 197946 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6QR | SA46QR | sa4 6qr | sa46qr | Swansea |  | Llannant |  | 1368 | 1200-1500 | 2.7381 | 2.0035 | 1.4692 | 25.4974 | 13.5986 | 15.03 | 258029 | 197972 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6QS | SA46QS | sa4 6qs | sa46qs | Swansea |  | Llannant |  | 1376 | 1200-1500 | 2.7541 | 2.0152 | 1.4778 | 25.6465 | 13.6781 | 15.1179 | 258035 | 198033 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6QZ | SA46QZ | sa4 6qz | sa46qz | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257677 | 198177 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6RP | SA46RP | sa4 6rp | sa46rp | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257906 | 198556 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6RQ | SA46RQ | sa4 6rq | sa46rq | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257559 | 198183 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6RR | SA46RR | sa4 6rr | sa46rr | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257891 | 198494 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6RS | SA46RS | sa4 6rs | sa46rs | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257802 | 198511 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6SL | SA46SL | sa4 6sl | sa46sl | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257295 | 198175 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6SP | SA46SP | sa4 6sp | sa46sp | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257325 | 198110 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6SR | SA46SR | sa4 6sr | sa46sr | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257607 | 198095 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6SS | SA46SS | sa4 6ss | sa46ss | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257631 | 198191 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6TE | SA46TE | sa4 6te | sa46te | Swansea |  | Llannant |  | 1340 | 1200-1500 | 2.6821 | 1.9625 | 1.4392 | 24.9755 | 13.3203 | 14.7224 | 257323 | 198898 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 6TH | SA46TH | sa4 6th | sa46th | Swansea |  | Llannant |  | 1312 | 1200-1500 | 2.626 | 1.9215 | 1.4091 | 24.4536 | 13.0419 | 14.4148 | 257682 | 199049 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8AB | SA48AB | sa4 8ab | sa48ab | Swansea |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258992 | 203986 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8AD | SA48AD | sa4 8ad | sa48ad | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259149 | 203919 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8AE | SA48AE | sa4 8ae | sa48ae | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259111 | 203916 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8AF | SA48AF | sa4 8af | sa48af | Swansea |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 259012 | 203978 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8AG | SA48AG | sa4 8ag | sa48ag | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259046 | 203979 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8AJ | SA48AJ | sa4 8aj | sa48aj | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259394 | 203373 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8BA | SA48BA | sa4 8ba | sa48ba | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259942 | 203045 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8BH | SA48BH | sa4 8bh | sa48bh | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259900 | 203053 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8BL | SA48BL | sa4 8bl | sa48bl | Swansea |  | Llannant |  | 1352 | 1200-1500 | 2.7061 | 1.9801 | 1.452 | 25.1992 | 13.4396 | 14.8542 | 259864 | 202968 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8BW | SA48BW | sa4 8bw | sa48bw | Swansea |  | Llannant |  | 1352 | 1200-1500 | 2.7061 | 1.9801 | 1.452 | 25.1992 | 13.4396 | 14.8542 | 259946 | 202966 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8DA | SA48DA | sa4 8da | sa48da | Swansea |  | Llannant |  | 1336 | 1200-1500 | 2.6741 | 1.9566 | 1.4349 | 24.9009 | 13.2805 | 14.6785 | 259254 | 201094 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8DB | SA48DB | sa4 8db | sa48db | Swansea |  | Llannant |  | 1316 | 1200-1500 | 2.634 | 1.9273 | 1.4134 | 24.5282 | 13.0817 | 14.4587 | 258855 | 201046 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8DD | SA48DD | sa4 8dd | sa48dd | Swansea |  | Llannant |  | 1336 | 1200-1500 | 2.6741 | 1.9566 | 1.4349 | 24.9009 | 13.2805 | 14.6785 | 259208 | 201544 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8DE | SA48DE | sa4 8de | sa48de | Swansea |  | Llannant |  | 1336 | 1200-1500 | 2.6741 | 1.9566 | 1.4349 | 24.9009 | 13.2805 | 14.6785 | 259318 | 201084 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8DF | SA48DF | sa4 8df | sa48df | Swansea |  | Llannant |  | 1336 | 1200-1500 | 2.6741 | 1.9566 | 1.4349 | 24.9009 | 13.2805 | 14.6785 | 259271 | 201128 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8DH | SA48DH | sa4 8dh | sa48dh | Swansea |  | Llannant |  | 1322 | 1200-1500 | 2.646 | 1.9361 | 1.4198 | 24.64 | 13.1413 | 14.5246 | 258514 | 202298 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8DJ | SA48DJ | sa4 8dj | sa48dj | Swansea |  | Llannant |  | 1316 | 1200-1500 | 2.634 | 1.9273 | 1.4134 | 24.5282 | 13.0817 | 14.4587 | 258536 | 201863 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8DQ | SA48DQ | sa4 8dq | sa48dq | Swansea |  | Llannant |  | 1322 | 1200-1500 | 2.646 | 1.9361 | 1.4198 | 24.64 | 13.1413 | 14.5246 | 258996 | 201978 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8DR | SA48DR | sa4 8dr | sa48dr | Swansea |  | Llannant |  | 1336 | 1200-1500 | 2.6741 | 1.9566 | 1.4349 | 24.9009 | 13.2805 | 14.6785 | 259020 | 201077 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8DS | SA48DS | sa4 8ds | sa48ds | Swansea |  | Llannant |  | 1396 | 1200-1500 | 2.7941 | 2.0445 | 1.4993 | 26.0192 | 13.8769 | 15.3377 | 260187 | 202018 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8DU | SA48DU | sa4 8du | sa48du | Swansea |  | Llannant |  | 1396 | 1200-1500 | 2.7941 | 2.0445 | 1.4993 | 26.0192 | 13.8769 | 15.3377 | 260629 | 202399 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8DX | SA48DX | sa4 8dx | sa48dx | Swansea |  | Llannant |  | 1396 | 1200-1500 | 2.7941 | 2.0445 | 1.4993 | 26.0192 | 13.8769 | 15.3377 | 260428 | 202695 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8EA | SA48EA | sa4 8ea | sa48ea | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259689 | 203047 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8EB | SA48EB | sa4 8eb | sa48eb | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259770 | 203045 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8ED | SA48ED | sa4 8ed | sa48ed | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259796 | 203128 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8EE | SA48EE | sa4 8ee | sa48ee | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259725 | 203180 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8EF | SA48EF | sa4 8ef | sa48ef | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259868 | 203130 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8EG | SA48EG | sa4 8eg | sa48eg | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259682 | 203142 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8EH | SA48EH | sa4 8eh | sa48eh | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259649 | 203080 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8HJ | SA48HJ | sa4 8hj | sa48hj | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259581 | 203186 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8HR | SA48HR | sa4 8hr | sa48hr | Swansea |  | Llannant |  | 1352 | 1200-1500 | 2.7061 | 1.9801 | 1.452 | 25.1992 | 13.4396 | 14.8542 | 259569 | 202888 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8HS | SA48HS | sa4 8hs | sa48hs | Swansea |  | Llannant |  | 1352 | 1200-1500 | 2.7061 | 1.9801 | 1.452 | 25.1992 | 13.4396 | 14.8542 | 259643 | 202925 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8HT | SA48HT | sa4 8ht | sa48ht | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259537 | 203139 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8HU | SA48HU | sa4 8hu | sa48hu | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259609 | 203516 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8HX | SA48HX | sa4 8hx | sa48hx | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259845 | 203552 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8HY | SA48HY | sa4 8hy | sa48hy | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259728 | 203478 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8HZ | SA48HZ | sa4 8hz | sa48hz | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259839 | 203445 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JA | SA48JA | sa4 8ja | sa48ja | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259669 | 203542 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JB | SA48JB | sa4 8jb | sa48jb | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259977 | 203102 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JD | SA48JD | sa4 8jd | sa48jd | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259945 | 203476 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JE | SA48JE | sa4 8je | sa48je | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259631 | 203344 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JF | SA48JF | sa4 8jf | sa48jf | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259827 | 203251 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JG | SA48JG | sa4 8jg | sa48jg | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259582 | 203232 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JH | SA48JH | sa4 8jh | sa48jh | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259489 | 203035 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JJ | SA48JJ | sa4 8jj | sa48jj | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 260009 | 203274 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JL | SA48JL | sa4 8jl | sa48jl | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260018 | 203077 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JN | SA48JN | sa4 8jn | sa48jn | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260120 | 203327 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JP | SA48JP | sa4 8jp | sa48jp | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260107 | 203070 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JQ | SA48JQ | sa4 8jq | sa48jq | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259716 | 203343 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JR | SA48JR | sa4 8jr | sa48jr | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259708 | 203418 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JS | SA48JS | sa4 8js | sa48js | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260207 | 203420 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JT | SA48JT | sa4 8jt | sa48jt | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259826 | 203369 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JU | SA48JU | sa4 8ju | sa48ju | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260287 | 203220 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JW | SA48JW | sa4 8jw | sa48jw | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260191 | 203622 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JX | SA48JX | sa4 8jx | sa48jx | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260182 | 203142 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JY | SA48JY | sa4 8jy | sa48jy | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260199 | 203253 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8JZ | SA48JZ | sa4 8jz | sa48jz | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259938 | 203021 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LA | SA48LA | sa4 8la | sa48la | Swansea |  | Llannant |  | 1336 | 1200-1500 | 2.6741 | 1.9566 | 1.4349 | 24.9009 | 13.2805 | 14.6785 | 259133 | 201060 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LD | SA48LD | sa4 8ld | sa48ld | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259354 | 203616 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LE | SA48LE | sa4 8le | sa48le | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259504 | 203533 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LF | SA48LF | sa4 8lf | sa48lf | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 260004 | 203627 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LG | SA48LG | sa4 8lg | sa48lg | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259487 | 203293 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LH | SA48LH | sa4 8lh | sa48lh | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259361 | 203508 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LL | SA48LL | sa4 8ll | sa48ll | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259287 | 203413 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LN | SA48LN | sa4 8ln | sa48ln | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259446 | 203614 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LP | SA48LP | sa4 8lp | sa48lp | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259349 | 203661 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LQ | SA48LQ | sa4 8lq | sa48lq | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259484 | 203399 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LR | SA48LR | sa4 8lr | sa48lr | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259534 | 203640 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LS | SA48LS | sa4 8ls | sa48ls | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259561 | 203700 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LT | SA48LT | sa4 8lt | sa48lt | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259586 | 203720 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LU | SA48LU | sa4 8lu | sa48lu | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259954 | 203657 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LW | SA48LW | sa4 8lw | sa48lw | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259477 | 203571 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LX | SA48LX | sa4 8lx | sa48lx | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259742 | 203728 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LY | SA48LY | sa4 8ly | sa48ly | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259823 | 203881 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8LZ | SA48LZ | sa4 8lz | sa48lz | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259944 | 203913 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8NA | SA48NA | sa4 8na | sa48na | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259885 | 204088 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8NB | SA48NB | sa4 8nb | sa48nb | Swansea |  | Llannant |  | 1455 | 1200-1500 | 2.9122 | 2.1309 | 1.5627 | 27.1189 | 14.4634 | 15.9859 | 260021 | 204028 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8ND | SA48ND | sa4 8nd | sa48nd | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259978 | 203825 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8NE | SA48NE | sa4 8ne | sa48ne | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260015 | 203821 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8NF | SA48NF | sa4 8nf | sa48nf | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260026 | 203782 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8NG | SA48NG | sa4 8ng | sa48ng | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260064 | 203765 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8NH | SA48NH | sa4 8nh | sa48nh | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260368 | 203777 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8NJ | SA48NJ | sa4 8nj | sa48nj | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260701 | 203863 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8NQ | SA48NQ | sa4 8nq | sa48nq | Swansea |  | Llannant |  | 1453 | 1200-1500 | 2.9082 | 2.128 | 1.5605 | 27.0816 | 14.4435 | 15.9639 | 260146 | 203875 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8NT | SA48NT | sa4 8nt | sa48nt | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259289 | 203353 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8NU | SA48NU | sa4 8nu | sa48nu | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259298 | 203306 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8NW | SA48NW | sa4 8nw | sa48nw | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259943 | 203724 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8NZ | SA48NZ | sa4 8nz | sa48nz | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259883 | 203719 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PA | SA48PA | sa4 8pa | sa48pa | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259350 | 203755 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PB | SA48PB | sa4 8pb | sa48pb | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259473 | 203841 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PD | SA48PD | sa4 8pd | sa48pd | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259596 | 204032 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PE | SA48PE | sa4 8pe | sa48pe | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259701 | 203864 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PF | SA48PF | sa4 8pf | sa48pf | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259660 | 203839 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PG | SA48PG | sa4 8pg | sa48pg | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259767 | 204017 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PH | SA48PH | sa4 8ph | sa48ph | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259703 | 204014 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PJ | SA48PJ | sa4 8pj | sa48pj | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259750 | 204164 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PL | SA48PL | sa4 8pl | sa48pl | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259827 | 204009 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PN | SA48PN | sa4 8pn | sa48pn | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259838 | 204087 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PP | SA48PP | sa4 8pp | sa48pp | Swansea |  | Llannant |  | 1455 | 1200-1500 | 2.9122 | 2.1309 | 1.5627 | 27.1189 | 14.4634 | 15.9859 | 260057 | 204195 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PQ | SA48PQ | sa4 8pq | sa48pq | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259798 | 204028 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PR | SA48PR | sa4 8pr | sa48pr | Swansea |  | Llannant |  | 1455 | 1200-1500 | 2.9122 | 2.1309 | 1.5627 | 27.1189 | 14.4634 | 15.9859 | 260019 | 204100 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PS | SA48PS | sa4 8ps | sa48ps | Swansea |  | Llannant |  | 1455 | 1200-1500 | 2.9122 | 2.1309 | 1.5627 | 27.1189 | 14.4634 | 15.9859 | 260065 | 204124 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PT | SA48PT | sa4 8pt | sa48pt | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259890 | 204295 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PU | SA48PU | sa4 8pu | sa48pu | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259847 | 204539 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PW | SA48PW | sa4 8pw | sa48pw | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259783 | 204252 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PX | SA48PX | sa4 8px | sa48px | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259663 | 204351 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PY | SA48PY | sa4 8py | sa48py | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259899 | 204649 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8PZ | SA48PZ | sa4 8pz | sa48pz | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259976 | 204749 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8QA | SA48QA | sa4 8qa | sa48qa | Swansea |  | Llannant |  | 1455 | 1200-1500 | 2.9122 | 2.1309 | 1.5627 | 27.1189 | 14.4634 | 15.9859 | 260032 | 204626 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8QE | SA48QE | sa4 8qe | sa48qe | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259761 | 204834 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8QF | SA48QF | sa4 8qf | sa48qf | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259527 | 204840 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8QG | SA48QG | sa4 8qg | sa48qg | Swansea |  | Llannant |  | 1582 | Over1500 | 3.1664 | 2.3169 | 1.6991 | 29.486 | 15.7259 | 17.3812 | 260080 | 205298 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8QN | SA48QN | sa4 8qn | sa48qn | Swansea |  | Llannant |  | 1455 | 1200-1500 | 2.9122 | 2.1309 | 1.5627 | 27.1189 | 14.4634 | 15.9859 | 260372 | 204957 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8QT | SA48QT | sa4 8qt | sa48qt | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259105 | 203551 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8QU | SA48QU | sa4 8qu | sa48qu | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259151 | 203481 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8QX | SA48QX | sa4 8qx | sa48qx | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259069 | 203430 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RA | SA48RA | sa4 8ra | sa48ra | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259261 | 203550 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RB | SA48RB | sa4 8rb | sa48rb | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259208 | 203418 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RD | SA48RD | sa4 8rd | sa48rd | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259183 | 203502 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RE | SA48RE | sa4 8re | sa48re | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259190 | 203652 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RF | SA48RF | sa4 8rf | sa48rf | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259298 | 203594 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RG | SA48RG | sa4 8rg | sa48rg | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259138 | 203609 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RH | SA48RH | sa4 8rh | sa48rh | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259274 | 203703 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RJ | SA48RJ | sa4 8rj | sa48rj | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259032 | 203507 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RL | SA48RL | sa4 8rl | sa48rl | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259135 | 203802 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RN | SA48RN | sa4 8rn | sa48rn | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259317 | 203817 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RP | SA48RP | sa4 8rp | sa48rp | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259032 | 203436 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RR | SA48RR | sa4 8rr | sa48rr | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259080 | 203488 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RS | SA48RS | sa4 8rs | sa48rs | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259237 | 203821 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RT | SA48RT | sa4 8rt | sa48rt | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259302 | 203891 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RU | SA48RU | sa4 8ru | sa48ru | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259113 | 204124 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RW | SA48RW | sa4 8rw | sa48rw | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259392 | 203838 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RX | SA48RX | sa4 8rx | sa48rx | Swansea |  | Llannant |  | 1404 | 1200-1500 | 2.8102 | 2.0562 | 1.5079 | 26.1684 | 13.9565 | 15.4256 | 258997 | 204078 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RY | SA48RY | sa4 8ry | sa48ry | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259211 | 204225 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8RZ | SA48RZ | sa4 8rz | sa48rz | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259239 | 204251 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8SA | SA48SA | sa4 8sa | sa48sa | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259023 | 203543 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8SD | SA48SD | sa4 8sd | sa48sd | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259393 | 204204 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8SE | SA48SE | sa4 8se | sa48se | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259412 | 204685 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8SF | SA48SF | sa4 8sf | sa48sf | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259135 | 204513 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8SG | SA48SG | sa4 8sg | sa48sg | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259211 | 204526 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8SH | SA48SH | sa4 8sh | sa48sh | Swansea |  | Llannant |  | 1414 | 1200-1500 | 2.8302 | 2.0709 | 1.5186 | 26.3547 | 14.0559 | 15.5354 | 259173 | 204328 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8SL | SA48SL | sa4 8sl | sa48sl | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259433 | 203866 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8SP | SA48SP | sa4 8sp | sa48sp | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259238 | 203687 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8SR | SA48SR | sa4 8sr | sa48sr | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259152 | 203691 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8SS | SA48SS | sa4 8ss | sa48ss | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259118 | 203708 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8ST | SA48ST | sa4 8st | sa48st | Swansea |  | Llannant |  | 1370 | 1200-1500 | 2.7421 | 2.0064 | 1.4714 | 25.5346 | 13.6185 | 15.052 | 259071 | 203705 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8SY | SA48SY | sa4 8sy | sa48sy | Swansea |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258993 | 203758 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8SZ | SA48SZ | sa4 8sz | sa48sz | Swansea |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258944 | 203793 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8TA | SA48TA | sa4 8ta | sa48ta | Swansea |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258929 | 203639 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8TB | SA48TB | sa4 8tb | sa48tb | Swansea |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258999 | 203687 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8TE | SA48TE | sa4 8te | sa48te | Swansea |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 259013 | 203832 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8TF | SA48TF | sa4 8tf | sa48tf | Swansea |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258965 | 203385 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8TH | SA48TH | sa4 8th | sa48th | Swansea |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258863 | 203859 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8TJ | SA48TJ | sa4 8tj | sa48tj | Swansea |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258801 | 203958 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8TL | SA48TL | sa4 8tl | sa48tl | Swansea |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258800 | 203936 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 8TQ | SA48TQ | sa4 8tq | sa48tq | Swansea |  | Llannant |  | 1342 | 1200-1500 | 2.6861 | 1.9654 | 1.4413 | 25.0128 | 13.3401 | 14.7444 | 258912 | 203737 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 9DY | SA49DY | sa4 9dy | sa49dy | Swansea |  | Llannant |  | 1396 | 1200-1500 | 2.7941 | 2.0445 | 1.4993 | 26.0192 | 13.8769 | 15.3377 | 260770 | 202376 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA4 9HG | SA49HG | sa4 9hg | sa49hg | Swansea |  | Llannant |  | 1396 | 1200-1500 | 2.7941 | 2.0445 | 1.4993 | 26.0192 | 13.8769 | 15.3377 | 260705 | 202627 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA5 7LX | SA57LX | sa5 7lx | sa57lx | Swansea |  | Felindre |  | 1514 | Over1500 | 3.0303 | 2.2173 | 1.626 | 28.2186 | 15.0499 | 16.6341 | 263880 | 202086 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA5 7NA | SA57NA | sa5 7na | sa57na | Swansea |  | Felindre |  | 1514 | Over1500 | 3.0303 | 2.2173 | 1.626 | 28.2186 | 15.0499 | 16.6341 | 263796 | 202721 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA5 7NB | SA57NB | sa5 7nb | sa57nb | Swansea |  | Felindre |  | 1514 | Over1500 | 3.0303 | 2.2173 | 1.626 | 28.2186 | 15.0499 | 16.6341 | 263724 | 202785 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA5 7ND | SA57ND | sa5 7nd | sa57nd | Swansea |  | Felindre |  | 1514 | Over1500 | 3.0303 | 2.2173 | 1.626 | 28.2186 | 15.0499 | 16.6341 | 263877 | 202903 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA5 7NL | SA57NL | sa5 7nl | sa57nl | Swansea |  | Felindre |  | 1566 | Over1500 | 3.1344 | 2.2935 | 1.6819 | 29.1878 | 15.5668 | 17.2054 | 264436 | 202507 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA5 7NP | SA57NP | sa5 7np | sa57np | Swansea |  | Felindre |  | 1566 | Over1500 | 3.1344 | 2.2935 | 1.6819 | 29.1878 | 15.5668 | 17.2054 | 264539 | 202397 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA5 7PG | SA57PG | sa5 7pg | sa57pg | Swansea |  | Felindre |  | 1514 | Over1500 | 3.0303 | 2.2173 | 1.626 | 28.2186 | 15.0499 | 16.6341 | 263251 | 202903 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA5 7PH | SA57PH | sa5 7ph | sa57ph | Swansea |  | Felindre |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 263005 | 202826 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA5 7PJ | SA57PJ | sa5 7pj | sa57pj | Swansea |  | Felindre |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262468 | 202329 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA5 7PQ | SA57PQ | sa5 7pq | sa57pq | Swansea |  | Felindre |  | 1495 | 1200-1500 | 2.9923 | 2.1895 | 1.6056 | 27.8645 | 14.861 | 16.4254 | 262969 | 202833 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA5 7PR | SA57PR | sa5 7pr | sa57pr | Swansea |  | Felindre |  | 1621 | Over1500 | 3.2445 | 2.374 | 1.7409 | 30.2129 | 16.1135 | 17.8097 | 263571 | 203037 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA6 5RT | SA65RT | sa6 5rt | sa65rt | Swansea |  | Rhyd-Y-Pandy |  | 1585 | Over1500 | 3.1724 | 2.3213 | 1.7023 | 29.5419 | 15.7557 | 17.4142 | 267025 | 203661 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA6 6PB | SA66PB | sa6 6pb | sa66pb | Swansea |  | Rhyd-Y-Pandy |  | 1564 | Over1500 | 3.1304 | 2.2905 | 1.6797 | 29.1505 | 15.5469 | 17.1835 | 266613 | 202283 | Swansea LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor a Dinas Abertawe | Swansea Council
SA61 1AD | SA611AD | sa61 1ad | sa611ad | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194649 | 214236 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DH | SA611DH | sa61 1dh | sa611dh | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193250 | 215355 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DJ | SA611DJ | sa61 1dj | sa611dj | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193030 | 215359 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DL | SA611DL | sa61 1dl | sa611dl | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193381 | 215405 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DN | SA611DN | sa61 1dn | sa611dn | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193486 | 215336 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DQ | SA611DQ | sa61 1dq | sa611dq | Pembrokeshire |  | Merlins Bridge |  | 1258 | 1200-1500 | 2.5179 | 1.8424 | 1.3511 | 23.4471 | 12.5051 | 13.8215 | 192936 | 215396 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DR | SA611DR | sa61 1dr | sa611dr | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193626 | 215371 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DS | SA611DS | sa61 1ds | sa611ds | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193534 | 215381 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DT | SA611DT | sa61 1dt | sa611dt | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193703 | 215339 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DU | SA611DU | sa61 1du | sa611du | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193814 | 215375 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DW | SA611DW | sa61 1dw | sa611dw | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193695 | 215306 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DX | SA611DX | sa61 1dx | sa611dx | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194030 | 215364 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DY | SA611DY | sa61 1dy | sa611dy | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194154 | 215268 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DZ | SA611DZ | sa61 1dz | sa611dz | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194232 | 215342 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EB | SA611EB | sa61 1eb | sa611eb | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194107 | 214446 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1ED | SA611ED | sa61 1ed | sa611ed | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194304 | 214771 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EE | SA611EE | sa61 1ee | sa611ee | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194290 | 214436 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EF | SA611EF | sa61 1ef | sa611ef | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194177 | 214548 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EH | SA611EH | sa61 1eh | sa611eh | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194635 | 215051 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EJ | SA611EJ | sa61 1ej | sa611ej | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194632 | 214994 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EL | SA611EL | sa61 1el | sa611el | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194642 | 214844 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EN | SA611EN | sa61 1en | sa611en | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194293 | 214591 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EP | SA611EP | sa61 1ep | sa611ep | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194494 | 214882 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1ES | SA611ES | sa61 1es | sa611es | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194082 | 214763 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1ET | SA611ET | sa61 1et | sa611et | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194210 | 215038 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EU | SA611EU | sa61 1eu | sa611eu | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194059 | 214874 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EW | SA611EW | sa61 1ew | sa611ew | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194209 | 214702 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EX | SA611EX | sa61 1ex | sa611ex | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194024 | 214847 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EY | SA611EY | sa61 1ey | sa611ey | Pembrokeshire |  | Merlins Bridge |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 193739 | 214723 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EZ | SA611EZ | sa61 1ez | sa611ez | Pembrokeshire |  | Merlins Bridge |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 194017 | 214785 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1FA | SA611FA | sa61 1fa | sa611fa | Pembrokeshire |  | Merlins Bridge |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 193920 | 214595 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1FB | SA611FB | sa61 1fb | sa611fb | Pembrokeshire |  | Merlins Bridge |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 193998 | 214600 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1FD | SA611FD | sa61 1fd | sa611fd | Pembrokeshire |  | Merlins Bridge |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 193950 | 214541 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1FE | SA611FE | sa61 1fe | sa611fe | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194112 | 214633 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HA | SA611HA | sa61 1ha | sa611ha | Pembrokeshire |  | Merlins Bridge |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 193953 | 214912 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HG | SA611HG | sa61 1hg | sa611hg | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194162 | 214916 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HH | SA611HH | sa61 1hh | sa611hh | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194123 | 214901 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HJ | SA611HJ | sa61 1hj | sa611hj | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194075 | 215089 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HL | SA611HL | sa61 1hl | sa611hl | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194174 | 215098 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HN | SA611HN | sa61 1hn | sa611hn | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194718 | 214323 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HQ | SA611HQ | sa61 1hq | sa611hq | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193961 | 215034 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HS | SA611HS | sa61 1hs | sa611hs | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194022 | 215105 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HT | SA611HT | sa61 1ht | sa611ht | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193861 | 215107 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HU | SA611HU | sa61 1hu | sa611hu | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193986 | 215162 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HX | SA611HX | sa61 1hx | sa611hx | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194120 | 215204 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HY | SA611HY | sa61 1hy | sa611hy | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193965 | 215212 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1HZ | SA611HZ | sa61 1hz | sa611hz | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 193935 | 215309 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JA | SA611JA | sa61 1ja | sa611ja | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194305 | 215251 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JB | SA611JB | sa61 1jb | sa611jb | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194255 | 215168 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JD | SA611JD | sa61 1jd | sa611jd | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194200 | 215249 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JE | SA611JE | sa61 1je | sa611je | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194190 | 215228 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JF | SA611JF | sa61 1jf | sa611jf | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194264 | 215024 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JG | SA611JG | sa61 1jg | sa611jg | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194277 | 215067 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JH | SA611JH | sa61 1jh | sa611jh | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194735 | 214626 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JJ | SA611JJ | sa61 1jj | sa611jj | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194738 | 214455 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JL | SA611JL | sa61 1jl | sa611jl | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195096 | 214579 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JN | SA611JN | sa61 1jn | sa611jn | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194881 | 214490 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JP | SA611JP | sa61 1jp | sa611jp | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194767 | 214315 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JS | SA611JS | sa61 1js | sa611js | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194772 | 214228 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JT | SA611JT | sa61 1jt | sa611jt | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194863 | 214152 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JU | SA611JU | sa61 1ju | sa611ju | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194999 | 214226 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JW | SA611JW | sa61 1jw | sa611jw | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194827 | 214329 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1JX | SA611JX | sa61 1jx | sa611jx | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195157 | 214305 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LA | SA611LA | sa61 1la | sa611la | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 195017 | 214166 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LB | SA611LB | sa61 1lb | sa611lb | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195185 | 214033 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LD | SA611LD | sa61 1ld | sa611ld | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195139 | 214371 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LE | SA611LE | sa61 1le | sa611le | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195351 | 214323 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LG | SA611LG | sa61 1lg | sa611lg | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195480 | 214390 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LH | SA611LH | sa61 1lh | sa611lh | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195139 | 214420 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LJ | SA611LJ | sa61 1lj | sa611lj | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195316 | 214418 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LL | SA611LL | sa61 1ll | sa611ll | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195171 | 214246 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LN | SA611LN | sa61 1ln | sa611ln | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194924 | 214015 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LP | SA611LP | sa61 1lp | sa611lp | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195189 | 214180 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LQ | SA611LQ | sa61 1lq | sa611lq | Pembrokeshire |  | Merlins Bridge |  | 1236 | 1200-1500 | 2.4739 | 1.8102 | 1.3275 | 23.0371 | 12.2865 | 13.5798 | 195246 | 213960 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LR | SA611LR | sa61 1lr | sa611lr | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194801 | 214057 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LS | SA611LS | sa61 1ls | sa611ls | Pembrokeshire |  | Merlins Bridge |  | 1236 | 1200-1500 | 2.4739 | 1.8102 | 1.3275 | 23.0371 | 12.2865 | 13.5798 | 195064 | 213904 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LT | SA611LT | sa61 1lt | sa611lt | Pembrokeshire |  | Merlins Bridge |  | 1236 | 1200-1500 | 2.4739 | 1.8102 | 1.3275 | 23.0371 | 12.2865 | 13.5798 | 195089 | 213879 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LU | SA611LU | sa61 1lu | sa611lu | Pembrokeshire |  | Merlins Bridge |  | 1236 | 1200-1500 | 2.4739 | 1.8102 | 1.3275 | 23.0371 | 12.2865 | 13.5798 | 195056 | 213773 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LW | SA611LW | sa61 1lw | sa611lw | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194891 | 213987 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LX | SA611LX | sa61 1lx | sa611lx | Pembrokeshire |  | Merlins Bridge |  | 1236 | 1200-1500 | 2.4739 | 1.8102 | 1.3275 | 23.0371 | 12.2865 | 13.5798 | 195119 | 213791 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LY | SA611LY | sa61 1ly | sa611ly | Pembrokeshire |  | Merlins Bridge |  | 1236 | 1200-1500 | 2.4739 | 1.8102 | 1.3275 | 23.0371 | 12.2865 | 13.5798 | 195021 | 213740 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1LZ | SA611LZ | sa61 1lz | sa611lz | Pembrokeshire |  | Merlins Bridge |  | 1236 | 1200-1500 | 2.4739 | 1.8102 | 1.3275 | 23.0371 | 12.2865 | 13.5798 | 195021 | 213923 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NA | SA611NA | sa61 1na | sa611na | Pembrokeshire |  | Merlins Bridge |  | 1236 | 1200-1500 | 2.4739 | 1.8102 | 1.3275 | 23.0371 | 12.2865 | 13.5798 | 195090 | 213960 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NB | SA611NB | sa61 1nb | sa611nb | Pembrokeshire |  | Merlins Bridge |  | 1236 | 1200-1500 | 2.4739 | 1.8102 | 1.3275 | 23.0371 | 12.2865 | 13.5798 | 195238 | 213796 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1ND | SA611ND | sa61 1nd | sa611nd | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195091 | 214226 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NN | SA611NN | sa61 1nn | sa611nn | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195029 | 214093 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NW | SA611NW | sa61 1nw | sa611nw | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195082 | 214029 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NY | SA611NY | sa61 1ny | sa611ny | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194948 | 214978 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NZ | SA611NZ | sa61 1nz | sa611nz | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194912 | 214940 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PA | SA611PA | sa61 1pa | sa611pa | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195051 | 214962 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PD | SA611PD | sa61 1pd | sa611pd | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 195018 | 214912 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PH | SA611PH | sa61 1ph | sa611ph | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194798 | 214955 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PP | SA611PP | sa61 1pp | sa611pp | Pembrokeshire |  | Merlins Bridge |  | 1273 | 1200-1500 | 2.548 | 1.8644 | 1.3672 | 23.7267 | 12.6543 | 13.9863 | 194766 | 215024 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RQ | SA611RQ | sa61 1rq | sa611rq | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195539 | 214925 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RX | SA611RX | sa61 1rx | sa611rx | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195426 | 214927 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RY | SA611RY | sa61 1ry | sa611ry | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195567 | 214838 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SG | SA611SG | sa61 1sg | sa611sg | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195267 | 214891 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SN | SA611SN | sa61 1sn | sa611sn | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195717 | 214942 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SZ | SA611SZ | sa61 1sz | sa611sz | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194495 | 214611 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TJ | SA611TJ | sa61 1tj | sa611tj | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195536 | 214889 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TL | SA611TL | sa61 1tl | sa611tl | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195284 | 214841 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TZ | SA611TZ | sa61 1tz | sa611tz | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 196249 | 215504 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UA | SA611UA | sa61 1ua | sa611ua | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 196370 | 215502 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UE | SA611UE | sa61 1ue | sa611ue | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 196441 | 215529 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UF | SA611UF | sa61 1uf | sa611uf | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 196381 | 215543 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UH | SA611UH | sa61 1uh | sa611uh | Pembrokeshire |  | Merlins Bridge |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 195905 | 214871 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UP | SA611UP | sa61 1up | sa611up | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 196150 | 215057 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UT | SA611UT | sa61 1ut | sa611ut | Pembrokeshire |  | Merlins Bridge |  | 1270 | 1200-1500 | 2.542 | 1.86 | 1.364 | 23.6708 | 12.6244 | 13.9533 | 196578 | 215221 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XA | SA611XA | sa61 1xa | sa611xa | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194723 | 214795 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XB | SA611XB | sa61 1xb | sa611xb | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194613 | 214476 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XD | SA611XD | sa61 1xd | sa611xd | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194537 | 214364 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XE | SA611XE | sa61 1xe | sa611xe | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194464 | 214257 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XF | SA611XF | sa61 1xf | sa611xf | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194524 | 214285 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XG | SA611XG | sa61 1xg | sa611xg | Pembrokeshire |  | Merlins Bridge |  | 1214 | 1200-1500 | 2.4299 | 1.778 | 1.3038 | 22.6271 | 12.0678 | 13.3381 | 193251 | 213359 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XJ | SA611XJ | sa61 1xj | sa611xj | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194662 | 214203 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XN | SA611XN | sa61 1xn | sa611xn | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194681 | 214137 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XQ | SA611XQ | sa61 1xq | sa611xq | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194202 | 214306 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XR | SA611XR | sa61 1xr | sa611xr | Pembrokeshire |  | Merlins Bridge |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 193647 | 214080 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XT | SA611XT | sa61 1xt | sa611xt | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194650 | 214633 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1XU | SA611XU | sa61 1xu | sa611xu | Pembrokeshire |  | Merlins Bridge |  | 1208 | 1200-1500 | 2.4179 | 1.7692 | 1.2974 | 22.5152 | 12.0081 | 13.2721 | 194596 | 214578 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UT | SA612UT | sa61 2ut | sa612ut | Pembrokeshire |  | Merlins Bridge |  | 1254 | 1200-1500 | 2.5099 | 1.8365 | 1.3468 | 23.3726 | 12.4654 | 13.7775 | 194343 | 216216 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2XA | SA612XA | sa61 2xa | sa612xa | Pembrokeshire |  | Merlins Bridge |  | 1258 | 1200-1500 | 2.5179 | 1.8424 | 1.3511 | 23.4471 | 12.5051 | 13.8215 | 192808 | 215314 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3AF | SA623AF | sa62 3af | sa623af | PCNPA |  | Marloes |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 179437 | 208478 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3AS | SA623AS | sa62 3as | sa623as | PCNPA |  | Marloes |  | 1034 | 900-1200 | 2.0696 | 1.5143 | 1.1105 | 19.2721 | 10.2785 | 11.3604 | 180962 | 208264 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3AT | SA623AT | sa62 3at | sa623at | PCNPA |  | Marloes |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 179593 | 208140 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3AX | SA623AX | sa62 3ax | sa623ax | PCNPA |  | Marloes |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 179521 | 208313 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3AY | SA623AY | sa62 3ay | sa623ay | PCNPA |  | Marloes |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 179433 | 208508 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3AZ | SA623AZ | sa62 3az | sa623az | PCNPA |  | Marloes |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 179356 | 208395 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3BA | SA623BA | sa62 3ba | sa623ba | PCNPA |  | Marloes |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 179434 | 208410 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3BB | SA623BB | sa62 3bb | sa623bb | PCNPA |  | Marloes |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 179209 | 208529 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3BD | SA623BD | sa62 3bd | sa623bd | PCNPA |  | Marloes |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 179159 | 208554 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3BE | SA623BE | sa62 3be | sa623be | PCNPA |  | Marloes |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 179051 | 208610 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3BG | SA623BG | sa62 3bg | sa623bg | PCNPA |  | Marloes |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 179172 | 208595 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3BH | SA623BH | sa62 3bh | sa623bh | PCNPA |  | Marloes |  | 1053 | 900-1200 | 2.1076 | 1.5422 | 1.1309 | 19.6263 | 10.4673 | 11.5692 | 178545 | 208204 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3BQ | SA623BQ | sa62 3bq | sa623bq | PCNPA |  | Marloes |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 179142 | 208621 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3BW | SA623BW | sa62 3bw | sa623bw | Pembrokeshire |  | Tiers Cross |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 190719 | 210889 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3BY | SA623BY | sa62 3by | sa623by | Pembrokeshire |  | Tiers Cross |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 190781 | 210843 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3BZ | SA623BZ | sa62 3bz | sa623bz | Pembrokeshire |  | Tiers Cross |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 190363 | 211011 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3DA | SA623DA | sa62 3da | sa623da | Pembrokeshire |  | Tiers Cross |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 190604 | 210726 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3DB | SA623DB | sa62 3db | sa623db | Pembrokeshire |  | Tiers Cross |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 190594 | 210601 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3DD | SA623DD | sa62 3dd | sa623dd | Pembrokeshire |  | Tiers Cross |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 190562 | 210672 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3DE | SA623DE | sa62 3de | sa623de | Pembrokeshire |  | Tiers Cross |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 190512 | 210613 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3DF | SA623DF | sa62 3df | sa623df | PCNPA |  | Marloes |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 179550 | 208231 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3DG | SA623DG | sa62 3dg | sa623dg | Pembrokeshire |  | Tiers Cross |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 190445 | 210604 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3DH | SA623DH | sa62 3dh | sa623dh | Pembrokeshire |  | Tiers Cross |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 190296 | 210329 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3DR | SA623DR | sa62 3dr | sa623dr | PCNPA |  | St Ishmaels |  | 1053 | 900-1200 | 2.1076 | 1.5422 | 1.1309 | 19.6263 | 10.4673 | 11.5692 | 184279 | 207827 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3DW | SA623DW | sa62 3dw | sa623dw | Pembrokeshire |  | Tiers Cross |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 190436 | 210637 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3EG | SA623EG | sa62 3eg | sa623eg | Pembrokeshire |  | Tiers Cross |  | 1188 | 900-1200 | 2.3778 | 1.7399 | 1.2759 | 22.1425 | 11.8093 | 13.0524 | 189135 | 210761 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3ER | SA623ER | sa62 3er | sa623er | Pembrokeshire |  | Tiers Cross |  | 1200 | 1200-1500 | 2.4018 | 1.7574 | 1.2888 | 22.3661 | 11.9286 | 13.1842 | 191237 | 211394 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3ES | SA623ES | sa62 3es | sa623es | Pembrokeshire |  | Tiers Cross |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 190672 | 210712 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3QX | SA623QX | sa62 3qx | sa623qx | PCNPA |  | Dale |  | 1057 | 900-1200 | 2.1156 | 1.548 | 1.1352 | 19.7008 | 10.5071 | 11.6131 | 180720 | 206730 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3QY | SA623QY | sa62 3qy | sa623qy | PCNPA |  | Dale |  | 997 | 900-1200 | 1.9955 | 1.4601 | 1.0708 | 18.5825 | 9.9107 | 10.9539 | 181063 | 206249 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3QZ | SA623QZ | sa62 3qz | sa623qz | PCNPA |  | Dale |  | 997 | 900-1200 | 1.9955 | 1.4601 | 1.0708 | 18.5825 | 9.9107 | 10.9539 | 181208 | 206083 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3RA | SA623RA | sa62 3ra | sa623ra | PCNPA |  | Dale |  | 935 | 900-1200 | 1.8714 | 1.3693 | 1.0042 | 17.4269 | 9.2944 | 10.2727 | 181169 | 205969 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3RB | SA623RB | sa62 3rb | sa623rb | PCNPA |  | Dale |  | 935 | 900-1200 | 1.8714 | 1.3693 | 1.0042 | 17.4269 | 9.2944 | 10.2727 | 181137 | 205696 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3RD | SA623RD | sa62 3rd | sa623rd | PCNPA |  | Dale |  | 935 | 900-1200 | 1.8714 | 1.3693 | 1.0042 | 17.4269 | 9.2944 | 10.2727 | 181479 | 205329 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3RE | SA623RE | sa62 3re | sa623re | PCNPA |  | Dale |  | 935 | 900-1200 | 1.8714 | 1.3693 | 1.0042 | 17.4269 | 9.2944 | 10.2727 | 181077 | 205675 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3RF | SA623RF | sa62 3rf | sa623rf | PCNPA |  | Dale |  | 1021 | 900-1200 | 2.0436 | 1.4953 | 1.0965 | 19.0298 | 10.1492 | 11.2176 | 180966 | 205694 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3RG | SA623RG | sa62 3rg | sa623rg | PCNPA |  | Dale |  | 1021 | 900-1200 | 2.0436 | 1.4953 | 1.0965 | 19.0298 | 10.1492 | 11.2176 | 180897 | 205652 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3RH | SA623RH | sa62 3rh | sa623rh | PCNPA |  | Dale |  | 1021 | 900-1200 | 2.0436 | 1.4953 | 1.0965 | 19.0298 | 10.1492 | 11.2176 | 180849 | 205699 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3RJ | SA623RJ | sa62 3rj | sa623rj | PCNPA |  | Dale |  | 1021 | 900-1200 | 2.0436 | 1.4953 | 1.0965 | 19.0298 | 10.1492 | 11.2176 | 180725 | 205669 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3RL | SA623RL | sa62 3rl | sa623rl | PCNPA |  | Dale |  | 1021 | 900-1200 | 2.0436 | 1.4953 | 1.0965 | 19.0298 | 10.1492 | 11.2176 | 180169 | 205414 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3RN | SA623RN | sa62 3rn | sa623rn | PCNPA |  | Dale |  | 1021 | 900-1200 | 2.0436 | 1.4953 | 1.0965 | 19.0298 | 10.1492 | 11.2176 | 180909 | 205910 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3RQ | SA623RQ | sa62 3rq | sa623rq | PCNPA |  | Dale |  | 935 | 900-1200 | 1.8714 | 1.3693 | 1.0042 | 17.4269 | 9.2944 | 10.2727 | 181096 | 205646 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3SF | SA623SF | sa62 3sf | sa623sf | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183605 | 207339 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3SS | SA623SS | sa62 3ss | sa623ss | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183464 | 207820 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3ST | SA623ST | sa62 3st | sa623st | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183375 | 207450 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3SU | SA623SU | sa62 3su | sa623su | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183272 | 207437 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3SW | SA623SW | sa62 3sw | sa623sw | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183403 | 207493 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3SX | SA623SX | sa62 3sx | sa623sx | PCNPA |  | St Ishmaels |  | 1045 | 900-1200 | 2.0916 | 1.5304 | 1.1223 | 19.4772 | 10.3878 | 11.4813 | 182922 | 207491 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3SY | SA623SY | sa62 3sy | sa623sy | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183259 | 207256 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3SZ | SA623SZ | sa62 3sz | sa623sz | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183505 | 207282 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3TA | SA623TA | sa62 3ta | sa623ta | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183711 | 207163 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3TB | SA623TB | sa62 3tb | sa623tb | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183761 | 207107 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3TD | SA623TD | sa62 3td | sa623td | PCNPA |  | St Ishmaels |  | 981 | 900-1200 | 1.9635 | 1.4367 | 1.0536 | 18.2843 | 9.7516 | 10.7781 | 183596 | 206970 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3TE | SA623TE | sa62 3te | sa623te | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183476 | 207364 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3TG | SA623TG | sa62 3tg | sa623tg | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183392 | 207205 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3TJ | SA623TJ | sa62 3tj | sa623tj | PCNPA |  | St Ishmaels |  | 997 | 900-1200 | 1.9955 | 1.4601 | 1.0708 | 18.5825 | 9.9107 | 10.9539 | 181884 | 206744 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3TP | SA623TP | sa62 3tp | sa623tp | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183310 | 207271 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3TR | SA623TR | sa62 3tr | sa623tr | PCNPA |  | St Ishmaels |  | 1015 | 900-1200 | 2.0316 | 1.4865 | 1.0901 | 18.918 | 10.0896 | 11.1517 | 183185 | 207191 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 3XH | SA623XH | sa62 3xh | sa623xh | Pembrokeshire |  | Merlins Bridge |  | 1229 | 1200-1500 | 2.4599 | 1.7999 | 1.3199 | 22.9066 | 12.2169 | 13.5029 | 192570 | 214457 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4AA | SA624AA | sa62 4aa | sa624aa | Pembrokeshire |  | Uzmaston |  | 1212 | 1200-1500 | 2.4259 | 1.775 | 1.3017 | 22.5898 | 12.0479 | 13.3161 | 196962 | 214442 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4AB | SA624AB | sa62 4ab | sa624ab | Pembrokeshire |  | Uzmaston |  | 1242 | 1200-1500 | 2.4859 | 1.819 | 1.3339 | 23.1489 | 12.3461 | 13.6457 | 197031 | 214470 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4AE | SA624AE | sa62 4ae | sa624ae | Pembrokeshire |  | Uzmaston |  | 1242 | 1200-1500 | 2.4859 | 1.819 | 1.3339 | 23.1489 | 12.3461 | 13.6457 | 197220 | 214222 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4AG | SA624AG | sa62 4ag | sa624ag | PCNPA |  | Uzmaston |  | 1242 | 1200-1500 | 2.4859 | 1.819 | 1.3339 | 23.1489 | 12.3461 | 13.6457 | 197398 | 214023 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4AZ | SA624AZ | sa62 4az | sa624az | Pembrokeshire |  | Hook |  | 1226 | 1200-1500 | 2.4539 | 1.7955 | 1.3167 | 22.8507 | 12.187 | 13.4699 | 195948 | 211255 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EA | SA624EA | sa62 4ea | sa624ea | Pembrokeshire |  | Hook |  | 1226 | 1200-1500 | 2.4539 | 1.7955 | 1.3167 | 22.8507 | 12.187 | 13.4699 | 195444 | 211154 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4ET | SA624ET | sa62 4et | sa624et | Pembrokeshire |  | Hook |  | 1212 | 1200-1500 | 2.4259 | 1.775 | 1.3017 | 22.5898 | 12.0479 | 13.3161 | 196051 | 212252 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EU | SA624EU | sa62 4eu | sa624eu | Pembrokeshire |  | Hook |  | 1226 | 1200-1500 | 2.4539 | 1.7955 | 1.3167 | 22.8507 | 12.187 | 13.4699 | 195645 | 211222 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EX | SA624EX | sa62 4ex | sa624ex | Pembrokeshire |  | Hook |  | 1226 | 1200-1500 | 2.4539 | 1.7955 | 1.3167 | 22.8507 | 12.187 | 13.4699 | 195489 | 211228 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EY | SA624EY | sa62 4ey | sa624ey | Pembrokeshire |  | Hook |  | 1226 | 1200-1500 | 2.4539 | 1.7955 | 1.3167 | 22.8507 | 12.187 | 13.4699 | 195103 | 210938 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4FB | SA624FB | sa62 4fb | sa624fb | Pembrokeshire |  | Hook |  | 1226 | 1200-1500 | 2.4539 | 1.7955 | 1.3167 | 22.8507 | 12.187 | 13.4699 | 195721 | 211166 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HA | SA624HA | sa62 4ha | sa624ha | Pembrokeshire |  | Hook |  | 1226 | 1200-1500 | 2.4539 | 1.7955 | 1.3167 | 22.8507 | 12.187 | 13.4699 | 195831 | 211179 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HG | SA624HG | sa62 4hg | sa624hg | Pembrokeshire |  | Llangwm |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 198751 | 209707 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HH | SA624HH | sa62 4hh | sa624hh | Pembrokeshire |  | Llangwm |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 198973 | 209589 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HJ | SA624HJ | sa62 4hj | sa624hj | Pembrokeshire |  | Llangwm |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 198906 | 209796 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HP | SA624HP | sa62 4hp | sa624hp | Pembrokeshire |  | Llangwm |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 198939 | 209553 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HR | SA624HR | sa62 4hr | sa624hr | Pembrokeshire |  | Llangwm |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 199031 | 209490 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HS | SA624HS | sa62 4hs | sa624hs | Pembrokeshire |  | Llangwm |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 199069 | 209468 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HT | SA624HT | sa62 4ht | sa624ht | Pembrokeshire |  | Llangwm |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 199131 | 209412 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HU | SA624HU | sa62 4hu | sa624hu | Pembrokeshire |  | Llangwm |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 198972 | 209442 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HW | SA624HW | sa62 4hw | sa624hw | Pembrokeshire |  | Llangwm |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 198848 | 209827 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HX | SA624HX | sa62 4hx | sa624hx | Pembrokeshire |  | Llangwm |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 199000 | 209363 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4HY | SA624HY | sa62 4hy | sa624hy | Pembrokeshire |  | Llangwm |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 198869 | 209335 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JA | SA624JA | sa62 4ja | sa624ja | Pembrokeshire |  | Llangwm |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 199279 | 209291 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JB | SA624JB | sa62 4jb | sa624jb | Pembrokeshire |  | Llangwm |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 199450 | 209312 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JE | SA624JE | sa62 4je | sa624je | Pembrokeshire |  | Llangwm |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 199004 | 209300 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JF | SA624JF | sa62 4jf | sa624jf | Pembrokeshire |  | Llangwm |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 199292 | 209366 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JG | SA624JG | sa62 4jg | sa624jg | Pembrokeshire |  | Llangwm |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 199078 | 209244 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JH | SA624JH | sa62 4jh | sa624jh | Pembrokeshire |  | Llangwm |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 199122 | 209183 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JJ | SA624JJ | sa62 4jj | sa624jj | Pembrokeshire |  | Llangwm |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 199183 | 209175 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JL | SA624JL | sa62 4jl | sa624jl | Pembrokeshire |  | Llangwm |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 199206 | 209131 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JN | SA624JN | sa62 4jn | sa624jn | PCNPA |  | Llangwm |  | 1230 | 1200-1500 | 2.4619 | 1.8014 | 1.321 | 22.9253 | 12.2268 | 13.5138 | 199592 | 208903 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JP | SA624JP | sa62 4jp | sa624jp | Pembrokeshire |  | Llangwm |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 199043 | 209147 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4JQ | SA624JQ | sa62 4jq | sa624jq | PCNPA |  | Llangwm |  | 1250 | 1200-1500 | 2.5019 | 1.8307 | 1.3425 | 23.298 | 12.4256 | 13.7336 | 199003 | 208406 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JR | SA624JR | sa62 4jr | sa624jr | PCNPA |  | Llangwm |  | 1250 | 1200-1500 | 2.5019 | 1.8307 | 1.3425 | 23.298 | 12.4256 | 13.7336 | 198909 | 208800 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JS | SA624JS | sa62 4js | sa624js | PCNPA |  | Llangwm |  | 1250 | 1200-1500 | 2.5019 | 1.8307 | 1.3425 | 23.298 | 12.4256 | 13.7336 | 198598 | 208446 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JT | SA624JT | sa62 4jt | sa624jt | PCNPA |  | Llangwm |  | 1250 | 1200-1500 | 2.5019 | 1.8307 | 1.3425 | 23.298 | 12.4256 | 13.7336 | 199017 | 208516 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JU | SA624JU | sa62 4ju | sa624ju | PCNPA |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197719 | 211647 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4JW | SA624JW | sa62 4jw | sa624jw | Pembrokeshire |  | Llangwm |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 199119 | 209084 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LA | SA624LA | sa62 4la | sa624la | Pembrokeshire |  | Merlins Bridge |  | 1225 | 1200-1500 | 2.4519 | 1.7941 | 1.3156 | 22.8321 | 12.1771 | 13.4589 | 195009 | 213410 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LB | SA624LB | sa62 4lb | sa624lb | Pembrokeshire |  | Hook |  | 1233 | 1200-1500 | 2.4679 | 1.8058 | 1.3242 | 22.9812 | 12.2566 | 13.5468 | 195516 | 212534 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LD | SA624LD | sa62 4ld | sa624ld | Pembrokeshire |  | Hook |  | 1226 | 1200-1500 | 2.4539 | 1.7955 | 1.3167 | 22.8507 | 12.187 | 13.4699 | 195744 | 211532 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LE | SA624LE | sa62 4le | sa624le | Pembrokeshire |  | Hook |  | 1226 | 1200-1500 | 2.4539 | 1.7955 | 1.3167 | 22.8507 | 12.187 | 13.4699 | 195441 | 211444 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LF | SA624LF | sa62 4lf | sa624lf | Pembrokeshire |  | Hook |  | 1218 | 1200-1500 | 2.4379 | 1.7838 | 1.3081 | 22.7016 | 12.1075 | 13.382 | 198058 | 211072 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LG | SA624LG | sa62 4lg | sa624lg | Pembrokeshire |  | Hook |  | 1226 | 1200-1500 | 2.4539 | 1.7955 | 1.3167 | 22.8507 | 12.187 | 13.4699 | 195807 | 211346 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LH | SA624LH | sa62 4lh | sa624lh | PCNPA |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197092 | 211419 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 4LJ | SA624LJ | sa62 4lj | sa624lj | Pembrokeshire |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197198 | 211377 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LL | SA624LL | sa62 4ll | sa624ll | Pembrokeshire |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197746 | 211498 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LN | SA624LN | sa62 4ln | sa624ln | Pembrokeshire |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197672 | 211439 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LP | SA624LP | sa62 4lp | sa624lp | Pembrokeshire |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197727 | 211459 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LQ | SA624LQ | sa62 4lq | sa624lq | Pembrokeshire |  | Hook |  | 1226 | 1200-1500 | 2.4539 | 1.7955 | 1.3167 | 22.8507 | 12.187 | 13.4699 | 196348 | 211350 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LR | SA624LR | sa62 4lr | sa624lr | Pembrokeshire |  | Hook |  | 1218 | 1200-1500 | 2.4379 | 1.7838 | 1.3081 | 22.7016 | 12.1075 | 13.382 | 198286 | 211830 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LS | SA624LS | sa62 4ls | sa624ls | Pembrokeshire |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197789 | 211325 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LT | SA624LT | sa62 4lt | sa624lt | Pembrokeshire |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197935 | 211225 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LU | SA624LU | sa62 4lu | sa624lu | Pembrokeshire |  | Hook |  | 1218 | 1200-1500 | 2.4379 | 1.7838 | 1.3081 | 22.7016 | 12.1075 | 13.382 | 198365 | 211174 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LW | SA624LW | sa62 4lw | sa624lw | Pembrokeshire |  | Hook |  | 1218 | 1200-1500 | 2.4379 | 1.7838 | 1.3081 | 22.7016 | 12.1075 | 13.382 | 198267 | 211125 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LX | SA624LX | sa62 4lx | sa624lx | Pembrokeshire |  | Hook |  | 1218 | 1200-1500 | 2.4379 | 1.7838 | 1.3081 | 22.7016 | 12.1075 | 13.382 | 198391 | 211209 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LY | SA624LY | sa62 4ly | sa624ly | Pembrokeshire |  | Hook |  | 1218 | 1200-1500 | 2.4379 | 1.7838 | 1.3081 | 22.7016 | 12.1075 | 13.382 | 198190 | 211262 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4LZ | SA624LZ | sa62 4lz | sa624lz | Pembrokeshire |  | Hook |  | 1218 | 1200-1500 | 2.4379 | 1.7838 | 1.3081 | 22.7016 | 12.1075 | 13.382 | 198199 | 211141 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NA | SA624NA | sa62 4na | sa624na | Pembrokeshire |  | Hook |  | 1218 | 1200-1500 | 2.4379 | 1.7838 | 1.3081 | 22.7016 | 12.1075 | 13.382 | 198404 | 211140 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NB | SA624NB | sa62 4nb | sa624nb | Pembrokeshire |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197970 | 211049 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4ND | SA624ND | sa62 4nd | sa624nd | Pembrokeshire |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197907 | 210986 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NE | SA624NE | sa62 4ne | sa624ne | Pembrokeshire |  | Hook |  | 1233 | 1200-1500 | 2.4679 | 1.8058 | 1.3242 | 22.9812 | 12.2566 | 13.5468 | 197944 | 210966 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NF | SA624NF | sa62 4nf | sa624nf | Pembrokeshire |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197831 | 211392 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NG | SA624NG | sa62 4ng | sa624ng | Pembrokeshire |  | Hook |  | 1223 | 1200-1500 | 2.4479 | 1.7911 | 1.3135 | 22.7948 | 12.1572 | 13.4369 | 198450 | 210415 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NG | SA624NG | sa62 4ng | sa624ng | Pembrokeshire |  | Llangwm |  | 1223 | 1200-1500 | 2.4479 | 1.7911 | 1.3135 | 22.7948 | 12.1572 | 13.4369 | 198450 | 210415 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NQ | SA624NQ | sa62 4nq | sa624nq | Pembrokeshire |  | Llangwm |  | 1246 | 1200-1500 | 2.4939 | 1.8248 | 1.3382 | 23.2235 | 12.3859 | 13.6896 | 198018 | 208345 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NR | SA624NR | sa62 4nr | sa624nr | Pembrokeshire |  | Llangwm |  | 1246 | 1200-1500 | 2.4939 | 1.8248 | 1.3382 | 23.2235 | 12.3859 | 13.6896 | 197123 | 208874 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NS | SA624NS | sa62 4ns | sa624ns | Pembrokeshire |  | Llangwm |  | 1246 | 1200-1500 | 2.4939 | 1.8248 | 1.3382 | 23.2235 | 12.3859 | 13.6896 | 197361 | 208562 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NU | SA624NU | sa62 4nu | sa624nu | Pembrokeshire |  | Llangwm |  | 1246 | 1200-1500 | 2.4939 | 1.8248 | 1.3382 | 23.2235 | 12.3859 | 13.6896 | 197945 | 208410 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NW | SA624NW | sa62 4nw | sa624nw | Pembrokeshire |  | Llangwm |  | 1246 | 1200-1500 | 2.4939 | 1.8248 | 1.3382 | 23.2235 | 12.3859 | 13.6896 | 197889 | 208364 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NX | SA624NX | sa62 4nx | sa624nx | Pembrokeshire |  | Llangwm |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 198457 | 209053 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NY | SA624NY | sa62 4ny | sa624ny | Pembrokeshire |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197949 | 211081 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4NZ | SA624NZ | sa62 4nz | sa624nz | Pembrokeshire |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197697 | 211354 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PF | SA624PF | sa62 4pf | sa624pf | Pembrokeshire |  | Hook |  | 1196 | 900-1200 | 2.3938 | 1.7516 | 1.2845 | 22.2916 | 11.8888 | 13.1403 | 197251 | 211337 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5HA | SA625HA | sa62 5ha | sa625ha | Pembrokeshire |  | Mathry |  | 1211 | 1200-1500 | 2.4239 | 1.7736 | 1.3006 | 22.5711 | 12.0379 | 13.3051 | 187940 | 232041 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5HD | SA625HD | sa62 5hd | sa625hd | Pembrokeshire |  | Mathry |  | 1211 | 1200-1500 | 2.4239 | 1.7736 | 1.3006 | 22.5711 | 12.0379 | 13.3051 | 187825 | 232126 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5HF | SA625HF | sa62 5hf | sa625hf | Pembrokeshire |  | Mathry |  | 1211 | 1200-1500 | 2.4239 | 1.7736 | 1.3006 | 22.5711 | 12.0379 | 13.3051 | 187985 | 232142 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5HR | SA625HR | sa62 5hr | sa625hr | Pembrokeshire |  | Wolf'S Castle |  | 1265 | 1200-1500 | 2.5319 | 1.8526 | 1.3586 | 23.5776 | 12.5747 | 13.8984 | 190280 | 226727 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7AE | SA667AE | sa66 7ae | sa667ae | Pembrokeshire |  | Clynderwen |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 212304 | 221357 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NJ | SA667NJ | sa66 7nj | sa667nj | Pembrokeshire |  | Clynderwen |  | 1339 | 1200-1500 | 2.6801 | 1.961 | 1.4381 | 24.9569 | 13.3103 | 14.7114 | 212172 | 219473 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NL | SA667NL | sa66 7nl | sa667nl | Pembrokeshire |  | Clynderwen |  | 1339 | 1200-1500 | 2.6801 | 1.961 | 1.4381 | 24.9569 | 13.3103 | 14.7114 | 212534 | 219585 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7PP | SA667PP | sa66 7pp | sa667pp | Pembrokeshire |  | Clynderwen |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 212656 | 220644 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7SR | SA667SR | sa66 7sr | sa667sr | Pembrokeshire |  | Clynderwen |  | 1339 | 1200-1500 | 2.6801 | 1.961 | 1.4381 | 24.9569 | 13.3103 | 14.7114 | 212269 | 219951 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7ST | SA667ST | sa66 7st | sa667st | Pembrokeshire |  | Clynderwen |  | 1344 | 1200-1500 | 2.6901 | 1.9683 | 1.4435 | 25.05 | 13.36 | 14.7663 | 212416 | 220433 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7SZ | SA667SZ | sa66 7sz | sa667sz | Pembrokeshire |  | Clynderwen |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 212156 | 221326 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TA | SA667TA | sa66 7ta | sa667ta | Pembrokeshire |  | Clynderwen |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 212184 | 221325 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TB | SA667TB | sa66 7tb | sa667tb | Pembrokeshire |  | Clynderwen |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 212179 | 221365 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TD | SA667TD | sa66 7td | sa667td | Pembrokeshire |  | Clynderwen |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 212152 | 221379 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TE | SA667TE | sa66 7te | sa667te | Pembrokeshire |  | Clynderwen |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 212164 | 221422 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TQ | SA667TQ | sa66 7tq | sa667tq | Pembrokeshire |  | Clynderwen |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 212113 | 221703 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TR | SA667TR | sa66 7tr | sa667tr | Pembrokeshire |  | Clynderwen |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 212102 | 221789 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TS | SA667TS | sa66 7ts | sa667ts | Pembrokeshire |  | Clynderwen |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 212136 | 221905 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TW | SA667TW | sa66 7tw | sa667tw | Pembrokeshire |  | Clynderwen |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 212155 | 221640 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7BR | SA677BR | sa67 7br | sa677br | Pembrokeshire |  | Narberth West |  | 1357 | 1200-1500 | 2.7161 | 1.9874 | 1.4574 | 25.2923 | 13.4893 | 14.9092 | 211008 | 214923 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DH | SA677DH | sa67 7dh | sa677dh | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211195 | 214803 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DJ | SA677DJ | sa67 7dj | sa677dj | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211300 | 214848 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DL | SA677DL | sa67 7dl | sa677dl | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211211 | 214877 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DN | SA677DN | sa67 7dn | sa677dn | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211410 | 214871 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DP | SA677DP | sa67 7dp | sa677dp | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211416 | 214904 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DQ | SA677DQ | sa67 7dq | sa677dq | Pembrokeshire |  | Narberth West |  | 1380 | 1200-1500 | 2.7621 | 2.0211 | 1.4821 | 25.721 | 13.7179 | 15.1619 | 211256 | 215061 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DR | SA677DR | sa67 7dr | sa677dr | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211233 | 214754 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DS | SA677DS | sa67 7ds | sa677ds | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211286 | 214771 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DT | SA677DT | sa67 7dt | sa677dt | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211321 | 214719 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DU | SA677DU | sa67 7du | sa677du | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211475 | 214622 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DW | SA677DW | sa67 7dw | sa677dw | Pembrokeshire |  | Narberth West |  | 1392 | 1200-1500 | 2.7861 | 2.0386 | 1.495 | 25.9447 | 13.8372 | 15.2937 | 210967 | 215030 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DX | SA677DX | sa67 7dx | sa677dx | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211432 | 214727 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7EA | SA677EA | sa67 7ea | sa677ea | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211282 | 214667 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7EG | SA677EG | sa67 7eg | sa677eg | Pembrokeshire |  | Llanddewi Velfrey |  | 1401 | 1200-1500 | 2.8042 | 2.0518 | 1.5047 | 26.1124 | 13.9266 | 15.3926 | 215653 | 217233 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7EL | SA677EL | sa67 7el | sa677el | Pembrokeshire |  | Llanddewi Velfrey |  | 1431 | 1200-1500 | 2.8642 | 2.0958 | 1.5369 | 26.6716 | 14.2248 | 15.7222 | 215343 | 216740 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7ES | SA677ES | sa67 7es | sa677es | Pembrokeshire |  | Narberth West |  | 1380 | 1200-1500 | 2.7621 | 2.0211 | 1.4821 | 25.721 | 13.7179 | 15.1619 | 211056 | 215551 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7EU | SA677EU | sa67 7eu | sa677eu | Pembrokeshire |  | Narberth West |  | 1380 | 1200-1500 | 2.7621 | 2.0211 | 1.4821 | 25.721 | 13.7179 | 15.1619 | 211098 | 215201 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7FD | SA677FD | sa67 7fd | sa677fd | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211413 | 214647 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7FE | SA677FE | sa67 7fe | sa677fe | Pembrokeshire |  | Narberth West |  | 1380 | 1200-1500 | 2.7621 | 2.0211 | 1.4821 | 25.721 | 13.7179 | 15.1619 | 211633 | 214983 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7FG | SA677FG | sa67 7fg | sa677fg | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211515 | 214855 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7FH | SA677FH | sa67 7fh | sa677fh | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211552 | 214767 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7FJ | SA677FJ | sa67 7fj | sa677fj | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211505 | 214723 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7FL | SA677FL | sa67 7fl | sa677fl | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211576 | 214684 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7NX | SA677NX | sa67 7nx | sa677nx | Pembrokeshire |  | Narberth West |  | 1345 | 1200-1500 | 2.6921 | 1.9698 | 1.4445 | 25.0687 | 13.37 | 14.7773 | 212052 | 215872 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7PD | SA677PD | sa67 7pd | sa677pd | Pembrokeshire |  | Llanddewi Velfrey |  | 1431 | 1200-1500 | 2.8642 | 2.0958 | 1.5369 | 26.6716 | 14.2248 | 15.7222 | 215058 | 216731 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7PE | SA677PE | sa67 7pe | sa677pe | Pembrokeshire |  | Llanddewi Velfrey |  | 1338 | 1200-1500 | 2.6781 | 1.9596 | 1.437 | 24.9382 | 13.3004 | 14.7004 | 215219 | 218226 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7PG | SA677PG | sa67 7pg | sa677pg | Pembrokeshire |  | Llanddewi Velfrey |  | 1366 | 1200-1500 | 2.7341 | 2.0006 | 1.4671 | 25.4601 | 13.5787 | 15.0081 | 214798 | 216988 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8TA | SA678TA | sa67 8ta | sa678ta | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211929 | 214554 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8TX | SA678TX | sa67 8tx | sa678tx | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211861 | 214815 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8TY | SA678TY | sa67 8ty | sa678ty | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211985 | 214676 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8UA | SA678UA | sa67 8ua | sa678ua | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211928 | 214611 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8UF | SA678UF | sa67 8uf | sa678uf | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211984 | 214784 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8UU | SA678UU | sa67 8uu | sa678uu | Pembrokeshire |  | Llanddewi Velfrey |  | 1431 | 1200-1500 | 2.8642 | 2.0958 | 1.5369 | 26.6716 | 14.2248 | 15.7222 | 215710 | 216125 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8UW | SA678UW | sa67 8uw | sa678uw | Pembrokeshire |  | Narberth West |  | 1386 | 1200-1500 | 2.7741 | 2.0299 | 1.4886 | 25.8329 | 13.7775 | 15.2278 | 211967 | 214560 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0AA | SA680AA | sa68 0aa | sa680aa | Pembrokeshire |  | Langdon |  | 1328 | 1200-1500 | 2.658 | 1.9449 | 1.4263 | 24.7518 | 13.201 | 14.5906 | 211970 | 207328 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0AB | SA680AB | sa68 0ab | sa680ab | Pembrokeshire |  | Langdon |  | 1294 | 1200-1500 | 2.59 | 1.8951 | 1.3898 | 24.1181 | 12.863 | 14.217 | 213065 | 207202 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0AD | SA680AD | sa68 0ad | sa680ad | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212770 | 207178 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0AD | SA680AD | sa68 0ad | sa680ad | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212770 | 207178 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0AE | SA680AE | sa68 0ae | sa680ae | Pembrokeshire |  | Langdon |  | 1328 | 1200-1500 | 2.658 | 1.9449 | 1.4263 | 24.7518 | 13.201 | 14.5906 | 211496 | 207050 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0NL | SA680NL | sa68 0nl | sa680nl | Pembrokeshire |  | Reynalton |  | 1333 | 1200-1500 | 2.6681 | 1.9522 | 1.4316 | 24.845 | 13.2507 | 14.6455 | 208428 | 208534 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0PE | SA680PE | sa68 0pe | sa680pe | Pembrokeshire |  | Reynalton |  | 1375 | 1200-1500 | 2.7521 | 2.0137 | 1.4767 | 25.6278 | 13.6682 | 15.1069 | 209254 | 209014 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0PF | SA680PF | sa68 0pf | sa680pf | Pembrokeshire |  | Langdon |  | 1328 | 1200-1500 | 2.658 | 1.9449 | 1.4263 | 24.7518 | 13.201 | 14.5906 | 211443 | 207192 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0PG | SA680PG | sa68 0pg | sa680pg | Pembrokeshire |  | Reynalton |  | 1333 | 1200-1500 | 2.6681 | 1.9522 | 1.4316 | 24.845 | 13.2507 | 14.6455 | 208955 | 208857 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0PH | SA680PH | sa68 0ph | sa680ph | Pembrokeshire |  | Reynalton |  | 1334 | 1200-1500 | 2.6701 | 1.9537 | 1.4327 | 24.8637 | 13.2606 | 14.6565 | 209166 | 208634 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0QP | SA680QP | sa68 0qp | sa680qp | Pembrokeshire |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 212425 | 206467 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0QR | SA680QR | sa68 0qr | sa680qr | Pembrokeshire |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 212150 | 206409 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0QS | SA680QS | sa68 0qs | sa680qs | Pembrokeshire |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 212147 | 206353 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0QT | SA680QT | sa68 0qt | sa680qt | Pembrokeshire |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 212285 | 206310 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0QU | SA680QU | sa68 0qu | sa680qu | Pembrokeshire |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 212212 | 206250 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0QW | SA680QW | sa68 0qw | sa680qw | Pembrokeshire |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 212457 | 206426 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0QX | SA680QX | sa68 0qx | sa680qx | Pembrokeshire |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 212159 | 206263 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0QY | SA680QY | sa68 0qy | sa680qy | Pembrokeshire |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 212097 | 206212 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0QZ | SA680QZ | sa68 0qz | sa680qz | Pembrokeshire |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 212483 | 206606 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0RA | SA680RA | sa68 0ra | sa680ra | Pembrokeshire |  | Langdon |  | 1301 | 1200-1500 | 2.604 | 1.9054 | 1.3973 | 24.2486 | 12.9326 | 14.2939 | 211469 | 206122 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0SA | SA680SA | sa68 0sa | sa680sa | Pembrokeshire |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 211465 | 205947 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0SB | SA680SB | sa68 0sb | sa680sb | Pembrokeshire |  | Langdon |  | 1301 | 1200-1500 | 2.604 | 1.9054 | 1.3973 | 24.2486 | 12.9326 | 14.2939 | 211592 | 206070 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0SE | SA680SE | sa68 0se | sa680se | Pembrokeshire |  | Langdon |  | 1300 | 1200-1500 | 2.602 | 1.9039 | 1.3962 | 24.23 | 12.9226 | 14.2829 | 210852 | 206745 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0TS | SA680TS | sa68 0ts | sa680ts | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205270 | 203750 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0TW | SA680TW | sa68 0tw | sa680tw | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212644 | 207338 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0TZ | SA680TZ | sa68 0tz | sa680tz | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212995 | 207260 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UA | SA680UA | sa68 0ua | sa680ua | Pembrokeshire |  | Langdon |  | 1294 | 1200-1500 | 2.59 | 1.8951 | 1.3898 | 24.1181 | 12.863 | 14.217 | 213083 | 207309 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UB | SA680UB | sa68 0ub | sa680ub | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212622 | 207455 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UD | SA680UD | sa68 0ud | sa680ud | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212851 | 207464 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UE | SA680UE | sa68 0ue | sa680ue | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212562 | 207230 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UF | SA680UF | sa68 0uf | sa680uf | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212533 | 207250 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UG | SA680UG | sa68 0ug | sa680ug | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212789 | 207305 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UH | SA680UH | sa68 0uh | sa680uh | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212746 | 207246 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UJ | SA680UJ | sa68 0uj | sa680uj | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212835 | 207341 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UL | SA680UL | sa68 0ul | sa680ul | Pembrokeshire |  | Langdon |  | 1294 | 1200-1500 | 2.59 | 1.8951 | 1.3898 | 24.1181 | 12.863 | 14.217 | 213168 | 207276 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UN | SA680UN | sa68 0un | sa680un | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212952 | 207352 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UP | SA680UP | sa68 0up | sa680up | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212690 | 207386 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UQ | SA680UQ | sa68 0uq | sa680uq | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212742 | 207404 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UR | SA680UR | sa68 0ur | sa680ur | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212645 | 207561 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0US | SA680US | sa68 0us | sa680us | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212583 | 207887 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UT | SA680UT | sa68 0ut | sa680ut | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212692 | 207594 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UU | SA680UU | sa68 0uu | sa680uu | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212563 | 207702 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UW | SA680UW | sa68 0uw | sa680uw | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212715 | 207491 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UX | SA680UX | sa68 0ux | sa680ux | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212630 | 207730 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UY | SA680UY | sa68 0uy | sa680uy | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212461 | 207973 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0UZ | SA680UZ | sa68 0uz | sa680uz | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212519 | 207694 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XA | SA680XA | sa68 0xa | sa680xa | Pembrokeshire |  | Langdon |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 211571 | 208882 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XB | SA680XB | sa68 0xb | sa680xb | Pembrokeshire |  | Langdon |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 211697 | 208101 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XD | SA680XD | sa68 0xd | sa680xd | Pembrokeshire |  | Langdon |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 211621 | 208031 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XE | SA680XE | sa68 0xe | sa680xe | Pembrokeshire |  | Langdon |  | 1328 | 1200-1500 | 2.658 | 1.9449 | 1.4263 | 24.7518 | 13.201 | 14.5906 | 211736 | 207654 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XF | SA680XF | sa68 0xf | sa680xf | Pembrokeshire |  | Langdon |  | 1367 | 1200-1500 | 2.7361 | 2.002 | 1.4682 | 25.4787 | 13.5887 | 15.019 | 211647 | 208131 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XG | SA680XG | sa68 0xg | sa680xg | Pembrokeshire |  | Langdon |  | 1346 | 1200-1500 | 2.6941 | 1.9713 | 1.4456 | 25.0873 | 13.3799 | 14.7883 | 210991 | 208358 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XN | SA680XN | sa68 0xn | sa680xn | Pembrokeshire |  | Langdon |  | 1334 | 1200-1500 | 2.6701 | 1.9537 | 1.4327 | 24.8637 | 13.2606 | 14.6565 | 209671 | 208023 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XR | SA680XR | sa68 0xr | sa680xr | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212627 | 207135 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XS | SA680XS | sa68 0xs | sa680xs | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212678 | 207037 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XT | SA680XT | sa68 0xt | sa680xt | Pembrokeshire |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 212710 | 206679 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XU | SA680XU | sa68 0xu | sa680xu | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212466 | 207155 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XX | SA680XX | sa68 0xx | sa680xx | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212444 | 207268 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0XY | SA680XY | sa68 0xy | sa680xy | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212366 | 207301 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YA | SA680YA | sa68 0ya | sa680ya | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212324 | 207216 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YB | SA680YB | sa68 0yb | sa680yb | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212590 | 207268 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YD | SA680YD | sa68 0yd | sa680yd | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212269 | 207328 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YE | SA680YE | sa68 0ye | sa680ye | Pembrokeshire |  | Langdon |  | 1328 | 1200-1500 | 2.658 | 1.9449 | 1.4263 | 24.7518 | 13.201 | 14.5906 | 211752 | 207053 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YF | SA680YF | sa68 0yf | sa680yf | Pembrokeshire |  | Langdon |  | 1328 | 1200-1500 | 2.658 | 1.9449 | 1.4263 | 24.7518 | 13.201 | 14.5906 | 211700 | 207029 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YG | SA680YG | sa68 0yg | sa680yg | Pembrokeshire |  | Langdon |  | 1301 | 1200-1500 | 2.604 | 1.9054 | 1.3973 | 24.2486 | 12.9326 | 14.2939 | 211482 | 206936 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YH | SA680YH | sa68 0yh | sa680yh | Pembrokeshire |  | Langdon |  | 1328 | 1200-1500 | 2.658 | 1.9449 | 1.4263 | 24.7518 | 13.201 | 14.5906 | 211906 | 207292 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YJ | SA680YJ | sa68 0yj | sa680yj | Pembrokeshire |  | Langdon |  | 1328 | 1200-1500 | 2.658 | 1.9449 | 1.4263 | 24.7518 | 13.201 | 14.5906 | 211985 | 207252 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YL | SA680YL | sa68 0yl | sa680yl | Pembrokeshire |  | Langdon |  | 1328 | 1200-1500 | 2.658 | 1.9449 | 1.4263 | 24.7518 | 13.201 | 14.5906 | 211381 | 207279 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YN | SA680YN | sa68 0yn | sa680yn | Pembrokeshire |  | Langdon |  | 1328 | 1200-1500 | 2.658 | 1.9449 | 1.4263 | 24.7518 | 13.201 | 14.5906 | 211466 | 207233 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YP | SA680YP | sa68 0yp | sa680yp | Pembrokeshire |  | Langdon |  | 1328 | 1200-1500 | 2.658 | 1.9449 | 1.4263 | 24.7518 | 13.201 | 14.5906 | 211831 | 207197 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YQ | SA680YQ | sa68 0yq | sa680yq | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212223 | 207386 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YU | SA680YU | sa68 0yu | sa680yu | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212701 | 207178 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YW | SA680YW | sa68 0yw | sa680yw | Pembrokeshire |  | Langdon |  | 1328 | 1200-1500 | 2.658 | 1.9449 | 1.4263 | 24.7518 | 13.201 | 14.5906 | 211822 | 206997 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0YX | SA680YX | sa68 0yx | sa680yx | Pembrokeshire |  | Langdon |  | 1301 | 1200-1500 | 2.604 | 1.9054 | 1.3973 | 24.2486 | 12.9326 | 14.2939 | 211787 | 206895 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0ZA | SA680ZA | sa68 0za | sa680za | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212357 | 207439 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA68 0ZB | SA680ZB | sa68 0zb | sa680zb | Pembrokeshire |  | Langdon |  | 1325 | 1200-1500 | 2.652 | 1.9405 | 1.423 | 24.6959 | 13.1712 | 14.5576 | 212422 | 207384 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA69 9BD | SA699BD | sa69 9bd | sa699bd | PCNPA |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 213012 | 206063 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA69 9BH | SA699BH | sa69 9bh | sa699bh | Pembrokeshire |  | Langdon |  | 1301 | 1200-1500 | 2.604 | 1.9054 | 1.3973 | 24.2486 | 12.9326 | 14.2939 | 211962 | 206127 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA69 9BJ | SA699BJ | sa69 9bj | sa699bj | Pembrokeshire |  | Langdon |  | 1301 | 1200-1500 | 2.604 | 1.9054 | 1.3973 | 24.2486 | 12.9326 | 14.2939 | 211685 | 205988 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA69 9BL | SA699BL | sa69 9bl | sa699bl | Pembrokeshire |  | Langdon |  | 1292 | 1200-1500 | 2.586 | 1.8922 | 1.3876 | 24.0809 | 12.8431 | 14.195 | 211675 | 205894 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA69 9BW | SA699BW | sa69 9bw | sa699bw | Pembrokeshire |  | Langdon |  | 1301 | 1200-1500 | 2.604 | 1.9054 | 1.3973 | 24.2486 | 12.9326 | 14.2939 | 211825 | 206190 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA69 9BY | SA699BY | sa69 9by | sa699by | Pembrokeshire |  | Langdon |  | 1301 | 1200-1500 | 2.604 | 1.9054 | 1.3973 | 24.2486 | 12.9326 | 14.2939 | 211871 | 206296 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8AY | SA708AY | sa70 8ay | sa708ay | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205092 | 203137 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8DS | SA708DS | sa70 8ds | sa708ds | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205371 | 203173 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8ER | SA708ER | sa70 8er | sa708er | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205233 | 203173 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8PE | SA708PE | sa70 8pe | sa708pe | Pembrokeshire |  | Carew |  | 1178 | 900-1200 | 2.3578 | 1.7252 | 1.2652 | 21.9561 | 11.7099 | 12.9425 | 203998 | 202992 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8PG | SA708PG | sa70 8pg | sa708pg | Pembrokeshire |  | Carew |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 203924 | 202937 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8PH | SA708PH | sa70 8ph | sa708ph | Pembrokeshire |  | Carew |  | 1178 | 900-1200 | 2.3578 | 1.7252 | 1.2652 | 21.9561 | 11.7099 | 12.9425 | 203983 | 203133 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8PJ | SA708PJ | sa70 8pj | sa708pj | Pembrokeshire |  | Carew |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 204272 | 203123 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8PL | SA708PL | sa70 8pl | sa708pl | Pembrokeshire |  | Carew |  | 1178 | 900-1200 | 2.3578 | 1.7252 | 1.2652 | 21.9561 | 11.7099 | 12.9425 | 203782 | 203088 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8PN | SA708PN | sa70 8pn | sa708pn | Pembrokeshire |  | Carew |  | 1178 | 900-1200 | 2.3578 | 1.7252 | 1.2652 | 21.9561 | 11.7099 | 12.9425 | 203805 | 203166 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8SE | SA708SE | sa70 8se | sa708se | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205301 | 203306 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8SF | SA708SF | sa70 8sf | sa708sf | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205232 | 203358 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8SG | SA708SG | sa70 8sg | sa708sg | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205809 | 203279 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8SH | SA708SH | sa70 8sh | sa708sh | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205420 | 203340 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8SJ | SA708SJ | sa70 8sj | sa708sj | Pembrokeshire |  | Carew |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 204904 | 203564 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8SL | SA708SL | sa70 8sl | sa708sl | Pembrokeshire |  | Carew |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 204736 | 203709 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8SN | SA708SN | sa70 8sn | sa708sn | PCNPA |  | Carew |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 204683 | 203775 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA70 8SQ | SA708SQ | sa70 8sq | sa708sq | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205328 | 203294 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8SR | SA708SR | sa70 8sr | sa708sr | Pembrokeshire |  | Carew |  | 1193 | 900-1200 | 2.3878 | 1.7472 | 1.2813 | 22.2356 | 11.859 | 13.1073 | 204503 | 202879 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8SS | SA708SS | sa70 8ss | sa708ss | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205657 | 203310 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8SW | SA708SW | sa70 8sw | sa708sw | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205113 | 203326 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8SY | SA708SY | sa70 8sy | sa708sy | Pembrokeshire |  | Carew |  | 1217 | 1200-1500 | 2.4359 | 1.7823 | 1.3071 | 22.683 | 12.0976 | 13.371 | 206246 | 202658 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8SZ | SA708SZ | sa70 8sz | sa708sz | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205170 | 203382 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8TA | SA708TA | sa70 8ta | sa708ta | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205168 | 203313 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8TB | SA708TB | sa70 8tb | sa708tb | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205146 | 203291 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8TD | SA708TD | sa70 8td | sa708td | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205584 | 203345 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8TE | SA708TE | sa70 8te | sa708te | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205116 | 203193 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8TF | SA708TF | sa70 8tf | sa708tf | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205136 | 203444 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA70 8TQ | SA708TQ | sa70 8tq | sa708tq | Pembrokeshire |  | Carew |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 205538 | 203143 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AA | SA714AA | sa71 4aa | sa714aa | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199024 | 201196 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AB | SA714AB | sa71 4ab | sa714ab | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199075 | 201146 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AD | SA714AD | sa71 4ad | sa714ad | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199170 | 201069 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AE | SA714AE | sa71 4ae | sa714ae | Pembrokeshire |  | Pembroke Dock |  | 1161 | 900-1200 | 2.3238 | 1.7003 | 1.2469 | 21.6392 | 11.5409 | 12.7557 | 199286 | 200972 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AF | SA714AF | sa71 4af | sa714af | Pembrokeshire |  | Pembroke Dock |  | 1161 | 900-1200 | 2.3238 | 1.7003 | 1.2469 | 21.6392 | 11.5409 | 12.7557 | 199355 | 200896 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AG | SA714AG | sa71 4ag | sa714ag | Pembrokeshire |  | Pembroke Dock |  | 1161 | 900-1200 | 2.3238 | 1.7003 | 1.2469 | 21.6392 | 11.5409 | 12.7557 | 199597 | 200837 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AH | SA714AH | sa71 4ah | sa714ah | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199124 | 201233 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AN | SA714AN | sa71 4an | sa714an | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199225 | 201245 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AP | SA714AP | sa71 4ap | sa714ap | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199274 | 201196 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AQ | SA714AQ | sa71 4aq | sa714aq | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199482 | 201221 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AR | SA714AR | sa71 4ar | sa714ar | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199485 | 201072 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AS | SA714AS | sa71 4as | sa714as | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199451 | 201010 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AT | SA714AT | sa71 4at | sa714at | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199412 | 201109 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AU | SA714AU | sa71 4au | sa714au | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199436 | 201217 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AW | SA714AW | sa71 4aw | sa714aw | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199163 | 201188 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AX | SA714AX | sa71 4ax | sa714ax | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199331 | 201273 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AY | SA714AY | sa71 4ay | sa714ay | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199604 | 201185 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4AZ | SA714AZ | sa71 4az | sa714az | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199256 | 201305 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BA | SA714BA | sa71 4ba | sa714ba | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199383 | 201423 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BB | SA714BB | sa71 4bb | sa714bb | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199571 | 201400 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BD | SA714BD | sa71 4bd | sa714bd | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199513 | 201592 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BE | SA714BE | sa71 4be | sa714be | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199481 | 201394 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BG | SA714BG | sa71 4bg | sa714bg | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199544 | 201476 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BH | SA714BH | sa71 4bh | sa714bh | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199318 | 201455 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BJ | SA714BJ | sa71 4bj | sa714bj | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199366 | 201464 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BL | SA714BL | sa71 4bl | sa714bl | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199147 | 201386 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BN | SA714BN | sa71 4bn | sa714bn | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199249 | 201489 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BP | SA714BP | sa71 4bp | sa714bp | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199020 | 201310 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BS | SA714BS | sa71 4bs | sa714bs | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198870 | 201860 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BT | SA714BT | sa71 4bt | sa714bt | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198969 | 201715 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BU | SA714BU | sa71 4bu | sa714bu | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199295 | 201944 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BW | SA714BW | sa71 4bw | sa714bw | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199195 | 201321 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BX | SA714BX | sa71 4bx | sa714bx | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197170 | 201525 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BY | SA714BY | sa71 4by | sa714by | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198503 | 201660 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4BZ | SA714BZ | sa71 4bz | sa714bz | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197367 | 201749 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DA | SA714DA | sa71 4da | sa714da | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198569 | 201399 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DB | SA714DB | sa71 4db | sa714db | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198806 | 201314 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DE | SA714DE | sa71 4de | sa714de | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198692 | 201368 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DF | SA714DF | sa71 4df | sa714df | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198717 | 201358 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DG | SA714DG | sa71 4dg | sa714dg | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198966 | 201241 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DH | SA714DH | sa71 4dh | sa714dh | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198986 | 201133 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DJ | SA714DJ | sa71 4dj | sa714dj | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199090 | 200997 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DL | SA714DL | sa71 4dl | sa714dl | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198956 | 201081 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DN | SA714DN | sa71 4dn | sa714dn | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198943 | 201052 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DP | SA714DP | sa71 4dp | sa714dp | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198857 | 201071 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DQ | SA714DQ | sa71 4dq | sa714dq | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198974 | 201239 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DR | SA714DR | sa71 4dr | sa714dr | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198736 | 201195 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DS | SA714DS | sa71 4ds | sa714ds | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198880 | 201222 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DT | SA714DT | sa71 4dt | sa714dt | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198913 | 201219 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DU | SA714DU | sa71 4du | sa714du | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198843 | 201208 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DW | SA714DW | sa71 4dw | sa714dw | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198575 | 201395 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DX | SA714DX | sa71 4dx | sa714dx | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198798 | 201224 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DY | SA714DY | sa71 4dy | sa714dy | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198603 | 201357 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4DZ | SA714DZ | sa71 4dz | sa714dz | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198295 | 201104 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EA | SA714EA | sa71 4ea | sa714ea | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198321 | 201412 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EB | SA714EB | sa71 4eb | sa714eb | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198492 | 201275 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4ED | SA714ED | sa71 4ed | sa714ed | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198497 | 201192 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EE | SA714EE | sa71 4ee | sa714ee | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198553 | 201186 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EF | SA714EF | sa71 4ef | sa714ef | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198380 | 200993 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EG | SA714EG | sa71 4eg | sa714eg | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198168 | 201177 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EH | SA714EH | sa71 4eh | sa714eh | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198207 | 201010 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EJ | SA714EJ | sa71 4ej | sa714ej | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198352 | 201153 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EL | SA714EL | sa71 4el | sa714el | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198457 | 201125 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EN | SA714EN | sa71 4en | sa714en | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198437 | 201215 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EP | SA714EP | sa71 4ep | sa714ep | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198367 | 201272 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EQ | SA714EQ | sa71 4eq | sa714eq | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198220 | 201149 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4ER | SA714ER | sa71 4er | sa714er | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198349 | 201209 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4ES | SA714ES | sa71 4es | sa714es | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198292 | 201208 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4ET | SA714ET | sa71 4et | sa714et | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198228 | 201249 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EU | SA714EU | sa71 4eu | sa714eu | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198080 | 201266 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EW | SA714EW | sa71 4ew | sa714ew | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198251 | 201037 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EX | SA714EX | sa71 4ex | sa714ex | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198056 | 201158 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EY | SA714EY | sa71 4ey | sa714ey | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197926 | 201121 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4EZ | SA714EZ | sa71 4ez | sa714ez | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198299 | 200905 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4FB | SA714FB | sa71 4fb | sa714fb | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198414 | 201064 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4FD | SA714FD | sa71 4fd | sa714fd | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198544 | 201051 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4FE | SA714FE | sa71 4fe | sa714fe | Pembrokeshire |  | Pembroke Dock |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 197756 | 202283 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HA | SA714HA | sa71 4ha | sa714ha | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 198002 | 201043 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HB | SA714HB | sa71 4hb | sa714hb | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198104 | 201044 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HD | SA714HD | sa71 4hd | sa714hd | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198087 | 201150 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HH | SA714HH | sa71 4hh | sa714hh | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198607 | 201417 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HJ | SA714HJ | sa71 4hj | sa714hj | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198552 | 201442 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HL | SA714HL | sa71 4hl | sa714hl | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198733 | 201391 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HN | SA714HN | sa71 4hn | sa714hn | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198915 | 201314 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HP | SA714HP | sa71 4hp | sa714hp | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197427 | 201221 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HS | SA714HS | sa71 4hs | sa714hs | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197363 | 201262 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HT | SA714HT | sa71 4ht | sa714ht | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197184 | 201206 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HU | SA714HU | sa71 4hu | sa714hu | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197096 | 201171 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HW | SA714HW | sa71 4hw | sa714hw | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198962 | 201329 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4HX | SA714HX | sa71 4hx | sa714hx | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197358 | 201523 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JA | SA714JA | sa71 4ja | sa714ja | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197328 | 201587 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JB | SA714JB | sa71 4jb | sa714jb | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197452 | 201882 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JD | SA714JD | sa71 4jd | sa714jd | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197273 | 201507 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JE | SA714JE | sa71 4je | sa714je | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197247 | 201455 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JF | SA714JF | sa71 4jf | sa714jf | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197277 | 201415 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JG | SA714JG | sa71 4jg | sa714jg | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197292 | 201387 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JH | SA714JH | sa71 4jh | sa714jh | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197154 | 201366 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JJ | SA714JJ | sa71 4jj | sa714jj | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197275 | 201310 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JL | SA714JL | sa71 4jl | sa714jl | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197328 | 201288 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JN | SA714JN | sa71 4jn | sa714jn | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197423 | 201658 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JQ | SA714JQ | sa71 4jq | sa714jq | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197263 | 201334 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JS | SA714JS | sa71 4js | sa714js | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198410 | 201482 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4JX | SA714JX | sa71 4jx | sa714jx | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198462 | 201458 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LA | SA714LA | sa71 4la | sa714la | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198300 | 201546 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LB | SA714LB | sa71 4lb | sa714lb | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198231 | 201532 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LD | SA714LD | sa71 4ld | sa714ld | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198293 | 201491 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LE | SA714LE | sa71 4le | sa714le | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198095 | 201489 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LF | SA714LF | sa71 4lf | sa714lf | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198229 | 201505 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LG | SA714LG | sa71 4lg | sa714lg | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198091 | 201417 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LH | SA714LH | sa71 4lh | sa714lh | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198083 | 201338 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LL | SA714LL | sa71 4ll | sa714ll | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198063 | 201268 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LN | SA714LN | sa71 4ln | sa714ln | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 198019 | 201406 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LP | SA714LP | sa71 4lp | sa714lp | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 198012 | 201345 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LQ | SA714LQ | sa71 4lq | sa714lq | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198102 | 201271 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LR | SA714LR | sa71 4lr | sa714lr | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197842 | 201298 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LS | SA714LS | sa71 4ls | sa714ls | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197762 | 201350 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LT | SA714LT | sa71 4lt | sa714lt | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197550 | 201303 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LU | SA714LU | sa71 4lu | sa714lu | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197587 | 201397 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LW | SA714LW | sa71 4lw | sa714lw | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197985 | 201481 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LX | SA714LX | sa71 4lx | sa714lx | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197511 | 201369 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4LZ | SA714LZ | sa71 4lz | sa714lz | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197206 | 201214 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NA | SA714NA | sa71 4na | sa714na | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197382 | 201379 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NB | SA714NB | sa71 4nb | sa714nb | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197423 | 201395 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4ND | SA714ND | sa71 4nd | sa714nd | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197394 | 201545 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NE | SA714NE | sa71 4ne | sa714ne | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197462 | 201501 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NF | SA714NF | sa71 4nf | sa714nf | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197573 | 201524 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NG | SA714NG | sa71 4ng | sa714ng | Pembrokeshire |  | Pembroke Dock |  | 1164 | 900-1200 | 2.3298 | 1.7047 | 1.2501 | 21.6951 | 11.5707 | 12.7887 | 197521 | 201434 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NH | SA714NH | sa71 4nh | sa714nh | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198304 | 201768 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NN | SA714NN | sa71 4nn | sa714nn | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198316 | 201817 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NP | SA714NP | sa71 4np | sa714np | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198442 | 201497 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NQ | SA714NQ | sa71 4nq | sa714nq | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198311 | 201699 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NR | SA714NR | sa71 4nr | sa714nr | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198321 | 201577 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NT | SA714NT | sa71 4nt | sa714nt | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198356 | 201590 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NU | SA714NU | sa71 4nu | sa714nu | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198368 | 201716 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NX | SA714NX | sa71 4nx | sa714nx | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198425 | 201694 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NY | SA714NY | sa71 4ny | sa714ny | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198222 | 201806 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4NZ | SA714NZ | sa71 4nz | sa714nz | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198269 | 201741 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PA | SA714PA | sa71 4pa | sa714pa | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198311 | 201874 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PB | SA714PB | sa71 4pb | sa714pb | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198395 | 201787 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PD | SA714PD | sa71 4pd | sa714pd | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198383 | 201761 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PE | SA714PE | sa71 4pe | sa714pe | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198425 | 201757 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PF | SA714PF | sa71 4pf | sa714pf | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198894 | 201608 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PG | SA714PG | sa71 4pg | sa714pg | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198483 | 201739 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PJ | SA714PJ | sa71 4pj | sa714pj | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198531 | 201753 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PL | SA714PL | sa71 4pl | sa714pl | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198621 | 201726 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PN | SA714PN | sa71 4pn | sa714pn | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198706 | 201760 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PP | SA714PP | sa71 4pp | sa714pp | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198704 | 201657 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PQ | SA714PQ | sa71 4pq | sa714pq | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198542 | 201708 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PR | SA714PR | sa71 4pr | sa714pr | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198791 | 201704 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PS | SA714PS | sa71 4ps | sa714ps | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198814 | 201763 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PT | SA714PT | sa71 4pt | sa714pt | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198813 | 201800 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PU | SA714PU | sa71 4pu | sa714pu | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198752 | 201803 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PW | SA714PW | sa71 4pw | sa714pw | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198742 | 201605 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PX | SA714PX | sa71 4px | sa714px | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198741 | 201846 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PY | SA714PY | sa71 4py | sa714py | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198672 | 201836 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4PZ | SA714PZ | sa71 4pz | sa714pz | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198560 | 201654 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QA | SA714QA | sa71 4qa | sa714qa | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198627 | 201884 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QB | SA714QB | sa71 4qb | sa714qb | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198658 | 201940 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QD | SA714QD | sa71 4qd | sa714qd | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198551 | 201790 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QE | SA714QE | sa71 4qe | sa714qe | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198435 | 201813 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QF | SA714QF | sa71 4qf | sa714qf | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198843 | 202037 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QG | SA714QG | sa71 4qg | sa714qg | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198417 | 201865 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QH | SA714QH | sa71 4qh | sa714qh | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198475 | 201936 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QJ | SA714QJ | sa71 4qj | sa714qj | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198547 | 201930 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QL | SA714QL | sa71 4ql | sa714ql | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198515 | 202003 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QN | SA714QN | sa71 4qn | sa714qn | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198431 | 201988 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QP | SA714QP | sa71 4qp | sa714qp | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198421 | 202056 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QQ | SA714QQ | sa71 4qq | sa714qq | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198807 | 201922 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QR | SA714QR | sa71 4qr | sa714qr | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198392 | 202109 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QS | SA714QS | sa71 4qs | sa714qs | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198327 | 202138 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QT | SA714QT | sa71 4qt | sa714qt | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198319 | 201935 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QU | SA714QU | sa71 4qu | sa714qu | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198768 | 201633 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QX | SA714QX | sa71 4qx | sa714qx | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198834 | 201988 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4QY | SA714QY | sa71 4qy | sa714qy | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198516 | 202075 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4RE | SA714RE | sa71 4re | sa714re | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197930 | 203210 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4RG | SA714RG | sa71 4rg | sa714rg | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198068 | 202900 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4RJ | SA714RJ | sa71 4rj | sa714rj | Pembrokeshire |  | Pembroke Dock |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 197837 | 202385 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4RL | SA714RL | sa71 4rl | sa714rl | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198030 | 202558 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4SZ | SA714SZ | sa71 4sz | sa714sz | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198881 | 202229 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TA | SA714TA | sa71 4ta | sa714ta | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198725 | 202196 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TB | SA714TB | sa71 4tb | sa714tb | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198792 | 202127 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TD | SA714TD | sa71 4td | sa714td | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198754 | 202130 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TE | SA714TE | sa71 4te | sa714te | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198692 | 202147 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TG | SA714TG | sa71 4tg | sa714tg | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198693 | 202122 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TH | SA714TH | sa71 4th | sa714th | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198756 | 202093 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TJ | SA714TJ | sa71 4tj | sa714tj | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198746 | 202045 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TL | SA714TL | sa71 4tl | sa714tl | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198650 | 202335 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TN | SA714TN | sa71 4tn | sa714tn | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198448 | 202388 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TP | SA714TP | sa71 4tp | sa714tp | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198297 | 202373 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TQ | SA714TQ | sa71 4tq | sa714tq | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198243 | 202386 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TR | SA714TR | sa71 4tr | sa714tr | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198365 | 202491 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 4TS | SA714TS | sa71 4ts | sa714ts | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198233 | 202278 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5AH | SA715AH | sa71 5ah | sa715ah | PCNPA |  | Angle |  | 1119 | 900-1200 | 2.2397 | 1.6388 | 1.2018 | 20.8564 | 11.1234 | 12.2943 | 187918 | 201317 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5AJ | SA715AJ | sa71 5aj | sa715aj | PCNPA |  | Angle |  | 1119 | 900-1200 | 2.2397 | 1.6388 | 1.2018 | 20.8564 | 11.1234 | 12.2943 | 187454 | 201701 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5AN | SA715AN | sa71 5an | sa715an | PCNPA |  | Angle |  | 1069 | 900-1200 | 2.1396 | 1.5656 | 1.1481 | 19.9245 | 10.6264 | 11.745 | 186795 | 202680 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5AP | SA715AP | sa71 5ap | sa715ap | PCNPA |  | Angle |  | 1069 | 900-1200 | 2.1396 | 1.5656 | 1.1481 | 19.9245 | 10.6264 | 11.745 | 186707 | 202822 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5AR | SA715AR | sa71 5ar | sa715ar | PCNPA |  | Angle |  | 1072 | 900-1200 | 2.1456 | 1.57 | 1.1513 | 19.9804 | 10.6562 | 11.7779 | 186687 | 203004 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5AS | SA715AS | sa71 5as | sa715as | PCNPA |  | Angle |  | 1060 | 900-1200 | 2.1216 | 1.5524 | 1.1384 | 19.7567 | 10.5369 | 11.6461 | 187129 | 203036 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5AT | SA715AT | sa71 5at | sa715at | PCNPA |  | Angle |  | 1069 | 900-1200 | 2.1396 | 1.5656 | 1.1481 | 19.9245 | 10.6264 | 11.745 | 186456 | 202940 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5AU | SA715AU | sa71 5au | sa715au | PCNPA |  | Angle |  | 1072 | 900-1200 | 2.1456 | 1.57 | 1.1513 | 19.9804 | 10.6562 | 11.7779 | 186381 | 203035 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5AW | SA715AW | sa71 5aw | sa715aw | PCNPA |  | Angle |  | 1072 | 900-1200 | 2.1456 | 1.57 | 1.1513 | 19.9804 | 10.6562 | 11.7779 | 185888 | 202967 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5AX | SA715AX | sa71 5ax | sa715ax | PCNPA |  | Angle |  | 1072 | 900-1200 | 2.1456 | 1.57 | 1.1513 | 19.9804 | 10.6562 | 11.7779 | 186066 | 202988 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5AY | SA715AY | sa71 5ay | sa715ay | PCNPA |  | Angle |  | 1072 | 900-1200 | 2.1456 | 1.57 | 1.1513 | 19.9804 | 10.6562 | 11.7779 | 186265 | 203018 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5BA | SA715BA | sa71 5ba | sa715ba | PCNPA |  | Angle |  | 1069 | 900-1200 | 2.1396 | 1.5656 | 1.1481 | 19.9245 | 10.6264 | 11.745 | 186124 | 202973 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5BB | SA715BB | sa71 5bb | sa715bb | PCNPA |  | Angle |  | 1072 | 900-1200 | 2.1456 | 1.57 | 1.1513 | 19.9804 | 10.6562 | 11.7779 | 186078 | 203015 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5BD | SA715BD | sa71 5bd | sa715bd | PCNPA |  | Angle |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 185981 | 203018 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5BE | SA715BE | sa71 5be | sa715be | PCNPA |  | Angle |  | 1035 | 900-1200 | 2.0716 | 1.5158 | 1.1116 | 19.2908 | 10.2884 | 11.3714 | 185310 | 203549 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA71 5BP | SA715BP | sa71 5bp | sa715bp | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198927 | 200935 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5BQ | SA715BQ | sa71 5bq | sa715bq | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198962 | 200966 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5BS | SA715BS | sa71 5bs | sa715bs | Pembrokeshire |  | Pembroke Dock |  | 1169 | 900-1200 | 2.3398 | 1.712 | 1.2555 | 21.7883 | 11.6204 | 12.8436 | 198632 | 201104 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5EP | SA715EP | sa71 5ep | sa715ep | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 197901 | 200858 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JA | SA715JA | sa71 5ja | sa715ja | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 200000 | 201276 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JB | SA715JB | sa71 5jb | sa715jb | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199727 | 201381 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JD | SA715JD | sa71 5jd | sa715jd | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199654 | 201334 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JE | SA715JE | sa71 5je | sa715je | Pembrokeshire |  | Pembroke Dock |  | 1197 | 900-1200 | 2.3958 | 1.7531 | 1.2856 | 22.3102 | 11.8988 | 13.1513 | 200169 | 201028 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JF | SA715JF | sa71 5jf | sa715jf | Pembrokeshire |  | Pembroke Dock |  | 1197 | 900-1200 | 2.3958 | 1.7531 | 1.2856 | 22.3102 | 11.8988 | 13.1513 | 200083 | 201207 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JG | SA715JG | sa71 5jg | sa715jg | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199688 | 201276 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JH | SA715JH | sa71 5jh | sa715jh | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199976 | 201101 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JJ | SA715JJ | sa71 5jj | sa715jj | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199739 | 201057 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JL | SA715JL | sa71 5jl | sa715jl | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199929 | 201009 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JN | SA715JN | sa71 5jn | sa715jn | Pembrokeshire |  | Pembroke Dock |  | 1161 | 900-1200 | 2.3238 | 1.7003 | 1.2469 | 21.6392 | 11.5409 | 12.7557 | 199858 | 200934 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JP | SA715JP | sa71 5jp | sa715jp | Pembrokeshire |  | Pembroke Dock |  | 1161 | 900-1200 | 2.3238 | 1.7003 | 1.2469 | 21.6392 | 11.5409 | 12.7557 | 199784 | 200932 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JQ | SA715JQ | sa71 5jq | sa715jq | Pembrokeshire |  | Pembroke Dock |  | 1182 | 900-1200 | 2.3658 | 1.7311 | 1.2695 | 22.0306 | 11.7497 | 12.9865 | 199675 | 201243 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JT | SA715JT | sa71 5jt | sa715jt | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201726 | 200106 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JW | SA715JW | sa71 5jw | sa715jw | Pembrokeshire |  | Pembroke Dock |  | 1161 | 900-1200 | 2.3238 | 1.7003 | 1.2469 | 21.6392 | 11.5409 | 12.7557 | 199952 | 200944 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JX | SA715JX | sa71 5jx | sa715jx | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201399 | 200170 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JY | SA715JY | sa71 5jy | sa715jy | Pembrokeshire |  | Lamphey |  | 1171 | 900-1200 | 2.3438 | 1.715 | 1.2576 | 21.8256 | 11.6403 | 12.8656 | 201132 | 199600 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5JZ | SA715JZ | sa71 5jz | sa715jz | Pembrokeshire |  | Pembroke Dock |  | 1161 | 900-1200 | 2.3238 | 1.7003 | 1.2469 | 21.6392 | 11.5409 | 12.7557 | 199936 | 200889 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5LQ | SA715LQ | sa71 5lq | sa715lq | Pembrokeshire |  | Pembroke Dock |  | 1166 | 900-1200 | 2.3338 | 1.7077 | 1.2523 | 21.7324 | 11.5906 | 12.8107 | 200038 | 200838 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5NA | SA715NA | sa71 5na | sa715na | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201731 | 199985 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5NJ | SA715NJ | sa71 5nj | sa715nj | Pembrokeshire |  | Pembroke Dock |  | 1161 | 900-1200 | 2.3238 | 1.7003 | 1.2469 | 21.6392 | 11.5409 | 12.7557 | 199996 | 200587 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5NL | SA715NL | sa71 5nl | sa715nl | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201352 | 200259 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5NN | SA715NN | sa71 5nn | sa715nn | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201451 | 200340 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5NP | SA715NP | sa71 5np | sa715np | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201568 | 200141 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5NR | SA715NR | sa71 5nr | sa715nr | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201485 | 200434 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5NS | SA715NS | sa71 5ns | sa715ns | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201396 | 200554 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5NT | SA715NT | sa71 5nt | sa715nt | Pembrokeshire |  | Lamphey |  | 1229 | 1200-1500 | 2.4599 | 1.7999 | 1.3199 | 22.9066 | 12.2169 | 13.5029 | 201709 | 201097 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5NU | SA715NU | sa71 5nu | sa715nu | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201606 | 200563 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5NW | SA715NW | sa71 5nw | sa715nw | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201566 | 200282 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5NX | SA715NX | sa71 5nx | sa715nx | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201620 | 200486 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5NY | SA715NY | sa71 5ny | sa715ny | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201584 | 200418 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5PA | SA715PA | sa71 5pa | sa715pa | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201698 | 200631 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5PB | SA715PB | sa71 5pb | sa715pb | Pembrokeshire |  | Lamphey |  | 1174 | 900-1200 | 2.3498 | 1.7194 | 1.2609 | 21.8815 | 11.6701 | 12.8986 | 201913 | 200629 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5PF | SA715PF | sa71 5pf | sa715pf | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198850 | 200899 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5PR | SA715PR | sa71 5pr | sa715pr | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198642 | 200720 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5PS | SA715PS | sa71 5ps | sa715ps | Pembrokeshire |  | Pembroke Dock |  | 1161 | 900-1200 | 2.3238 | 1.7003 | 1.2469 | 21.6392 | 11.5409 | 12.7557 | 199041 | 200711 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5PT | SA715PT | sa71 5pt | sa715pt | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198995 | 200632 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5PZ | SA715PZ | sa71 5pz | sa715pz | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198765 | 200793 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5QB | SA715QB | sa71 5qb | sa715qb | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198870 | 200661 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5QD | SA715QD | sa71 5qd | sa715qd | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198810 | 200705 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5QE | SA715QE | sa71 5qe | sa715qe | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198825 | 200766 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5QG | SA715QG | sa71 5qg | sa715qg | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198714 | 200933 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5QH | SA715QH | sa71 5qh | sa715qh | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198870 | 200373 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5QJ | SA715QJ | sa71 5qj | sa715qj | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198936 | 200438 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5QL | SA715QL | sa71 5ql | sa715ql | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 199002 | 200450 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5QN | SA715QN | sa71 5qn | sa715qn | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198596 | 200856 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5QQ | SA715QQ | sa71 5qq | sa715qq | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198705 | 200863 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5QW | SA715QW | sa71 5qw | sa715qw | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198696 | 200804 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5QY | SA715QY | sa71 5qy | sa715qy | Pembrokeshire |  | Pembroke Dock |  | 1194 | 900-1200 | 2.3898 | 1.7487 | 1.2824 | 22.2543 | 11.869 | 13.1183 | 198560 | 200840 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RD | SA715RD | sa71 5rd | sa715rd | Pembrokeshire |  | Hundleton |  | 1186 | 900-1200 | 2.3738 | 1.7369 | 1.2738 | 22.1052 | 11.7894 | 13.0304 | 195856 | 200436 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RE | SA715RE | sa71 5re | sa715re | Pembrokeshire |  | Hundleton |  | 1190 | 900-1200 | 2.3818 | 1.7428 | 1.2781 | 22.1797 | 11.8292 | 13.0744 | 196053 | 200706 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RF | SA715RF | sa71 5rf | sa715rf | Pembrokeshire |  | Hundleton |  | 1186 | 900-1200 | 2.3738 | 1.7369 | 1.2738 | 22.1052 | 11.7894 | 13.0304 | 195812 | 200712 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RG | SA715RG | sa71 5rg | sa715rg | Pembrokeshire |  | Hundleton |  | 1190 | 900-1200 | 2.3818 | 1.7428 | 1.2781 | 22.1797 | 11.8292 | 13.0744 | 196213 | 200639 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RH | SA715RH | sa71 5rh | sa715rh | Pembrokeshire |  | Hundleton |  | 1190 | 900-1200 | 2.3818 | 1.7428 | 1.2781 | 22.1797 | 11.8292 | 13.0744 | 196107 | 200769 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RJ | SA715RJ | sa71 5rj | sa715rj | Pembrokeshire |  | Hundleton |  | 1190 | 900-1200 | 2.3818 | 1.7428 | 1.2781 | 22.1797 | 11.8292 | 13.0744 | 196220 | 200860 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RN | SA715RN | sa71 5rn | sa715rn | Pembrokeshire |  | Hundleton |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196128 | 201463 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RN | SA715RN | sa71 5rn | sa715rn | Pembrokeshire |  | Pembroke Dock |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196128 | 201463 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RP | SA715RP | sa71 5rp | sa715rp | Pembrokeshire |  | Hundleton |  | 1186 | 900-1200 | 2.3738 | 1.7369 | 1.2738 | 22.1052 | 11.7894 | 13.0304 | 195923 | 200896 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RQ | SA715RQ | sa71 5rq | sa715rq | Pembrokeshire |  | Hundleton |  | 1190 | 900-1200 | 2.3818 | 1.7428 | 1.2781 | 22.1797 | 11.8292 | 13.0744 | 196131 | 200696 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RR | SA715RR | sa71 5rr | sa715rr | Pembrokeshire |  | Hundleton |  | 1186 | 900-1200 | 2.3738 | 1.7369 | 1.2738 | 22.1052 | 11.7894 | 13.0304 | 195911 | 200678 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RW | SA715RW | sa71 5rw | sa715rw | Pembrokeshire |  | Hundleton |  | 1186 | 900-1200 | 2.3738 | 1.7369 | 1.2738 | 22.1052 | 11.7894 | 13.0304 | 195877 | 200800 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RY | SA715RY | sa71 5ry | sa715ry | Pembrokeshire |  | Hundleton |  | 1190 | 900-1200 | 2.3818 | 1.7428 | 1.2781 | 22.1797 | 11.8292 | 13.0744 | 196235 | 200701 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5RZ | SA715RZ | sa71 5rz | sa715rz | Pembrokeshire |  | Hundleton |  | 1186 | 900-1200 | 2.3738 | 1.7369 | 1.2738 | 22.1052 | 11.7894 | 13.0304 | 195969 | 200444 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5TS | SA715TS | sa71 5ts | sa715ts | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198585 | 202175 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5TT | SA715TT | sa71 5tt | sa715tt | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198561 | 202137 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5TU | SA715TU | sa71 5tu | sa715tu | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198614 | 202227 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5TX | SA715TX | sa71 5tx | sa715tx | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198463 | 202260 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA71 5TY | SA715TY | sa71 5ty | sa715ty | Pembrokeshire |  | Pembroke Dock |  | 1244 | 1200-1500 | 2.4899 | 1.8219 | 1.3361 | 23.1862 | 12.366 | 13.6677 | 198552 | 202088 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4AA | SA724AA | sa72 4aa | sa724aa | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197776 | 203563 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4RA | SA724RA | sa72 4ra | sa724ra | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 198195 | 203370 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4RR | SA724RR | sa72 4rr | sa724rr | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 198009 | 203660 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4RS | SA724RS | sa72 4rs | sa724rs | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197925 | 203354 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4RT | SA724RT | sa72 4rt | sa724rt | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 198139 | 203754 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4RZ | SA724RZ | sa72 4rz | sa724rz | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 198221 | 203513 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4SB | SA724SB | sa72 4sb | sa724sb | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200089 | 203156 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4SD | SA724SD | sa72 4sd | sa724sd | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200425 | 203253 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4SS | SA724SS | sa72 4ss | sa724ss | Pembrokeshire |  | Cosheston |  | 1235 | 1200-1500 | 2.4719 | 1.8087 | 1.3264 | 23.0185 | 12.2765 | 13.5688 | 200739 | 202906 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4SU | SA724SU | sa72 4su | sa724su | Pembrokeshire |  | Cosheston |  | 1201 | 1200-1500 | 2.4038 | 1.7589 | 1.2899 | 22.3848 | 11.9385 | 13.1952 | 201329 | 202970 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4SX | SA724SX | sa72 4sx | sa724sx | Pembrokeshire |  | Cosheston |  | 1235 | 1200-1500 | 2.4719 | 1.8087 | 1.3264 | 23.0185 | 12.2765 | 13.5688 | 200335 | 202645 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4TT | SA724TT | sa72 4tt | sa724tt | PCNPA |  | Cosheston |  | 1228 | 1200-1500 | 2.4579 | 1.7985 | 1.3189 | 22.888 | 12.2069 | 13.4919 | 200517 | 204026 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA72 4UA | SA724UA | sa72 4ua | sa724ua | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200535 | 203871 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4UB | SA724UB | sa72 4ub | sa724ub | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200529 | 203781 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4UD | SA724UD | sa72 4ud | sa724ud | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200661 | 203661 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4UE | SA724UE | sa72 4ue | sa724ue | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200677 | 203857 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4UF | SA724UF | sa72 4uf | sa724uf | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200744 | 203892 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4UG | SA724UG | sa72 4ug | sa724ug | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200927 | 203880 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4UH | SA724UH | sa72 4uh | sa724uh | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200419 | 203674 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4UJ | SA724UJ | sa72 4uj | sa724uj | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200278 | 203632 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4UL | SA724UL | sa72 4ul | sa724ul | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200339 | 203779 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4UN | SA724UN | sa72 4un | sa724un | Pembrokeshire |  | Cosheston |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 199877 | 203723 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4UQ | SA724UQ | sa72 4uq | sa724uq | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200971 | 203879 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4UR | SA724UR | sa72 4ur | sa724ur | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200640 | 203848 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4US | SA724US | sa72 4us | sa724us | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200304 | 203586 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 4UW | SA724UW | sa72 4uw | sa724uw | Pembrokeshire |  | Cosheston |  | 1205 | 1200-1500 | 2.4119 | 1.7648 | 1.2942 | 22.4593 | 11.9783 | 13.2392 | 200437 | 203802 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AE | SA726AE | sa72 6ae | sa726ae | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195635 | 203934 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AF | SA726AF | sa72 6af | sa726af | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197349 | 203647 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AG | SA726AG | sa72 6ag | sa726ag | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196767 | 203613 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AH | SA726AH | sa72 6ah | sa726ah | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196762 | 203538 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AL | SA726AL | sa72 6al | sa726al | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196726 | 203468 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AN | SA726AN | sa72 6an | sa726an | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196738 | 203344 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AQ | SA726AQ | sa72 6aq | sa726aq | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195691 | 202606 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AR | SA726AR | sa72 6ar | sa726ar | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196769 | 203215 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AS | SA726AS | sa72 6as | sa726as | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196685 | 203249 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AT | SA726AT | sa72 6at | sa726at | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196653 | 203220 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AU | SA726AU | sa72 6au | sa726au | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196610 | 203347 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AW | SA726AW | sa72 6aw | sa726aw | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196718 | 203323 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AX | SA726AX | sa72 6ax | sa726ax | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196531 | 203361 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6AY | SA726AY | sa72 6ay | sa726ay | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196446 | 203286 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6BA | SA726BA | sa72 6ba | sa726ba | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196448 | 203161 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6BB | SA726BB | sa72 6bb | sa726bb | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196532 | 203149 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6BD | SA726BD | sa72 6bd | sa726bd | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196734 | 203090 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6BE | SA726BE | sa72 6be | sa726be | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196819 | 203029 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6BH | SA726BH | sa72 6bh | sa726bh | Pembrokeshire |  | Pembroke Dock |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 197046 | 202965 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6BJ | SA726BJ | sa72 6bj | sa726bj | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196573 | 203081 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6BL | SA726BL | sa72 6bl | sa726bl | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196562 | 203251 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6BP | SA726BP | sa72 6bp | sa726bp | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197427 | 203499 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6BQ | SA726BQ | sa72 6bq | sa726bq | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196799 | 202987 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6BT | SA726BT | sa72 6bt | sa726bt | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196865 | 203546 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6BX | SA726BX | sa72 6bx | sa726bx | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196887 | 203549 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DA | SA726DA | sa72 6da | sa726da | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196831 | 203613 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DB | SA726DB | sa72 6db | sa726db | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196808 | 203635 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DD | SA726DD | sa72 6dd | sa726dd | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196810 | 203415 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DE | SA726DE | sa72 6de | sa726de | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196842 | 203325 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DF | SA726DF | sa72 6df | sa726df | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197320 | 204182 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DG | SA726DG | sa72 6dg | sa726dg | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196839 | 203220 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DH | SA726DH | sa72 6dh | sa726dh | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196934 | 203307 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DJ | SA726DJ | sa72 6dj | sa726dj | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196908 | 203389 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DL | SA726DL | sa72 6dl | sa726dl | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196878 | 203440 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DN | SA726DN | sa72 6dn | sa726dn | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196922 | 203612 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DP | SA726DP | sa72 6dp | sa726dp | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197030 | 203686 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DQ | SA726DQ | sa72 6dq | sa726dq | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196862 | 203218 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DR | SA726DR | sa72 6dr | sa726dr | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197047 | 203667 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DS | SA726DS | sa72 6ds | sa726ds | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197068 | 203705 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DT | SA726DT | sa72 6dt | sa726dt | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197199 | 203682 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DU | SA726DU | sa72 6du | sa726du | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197054 | 203750 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DW | SA726DW | sa72 6dw | sa726dw | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196970 | 203689 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DX | SA726DX | sa72 6dx | sa726dx | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197064 | 203878 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6DY | SA726DY | sa72 6dy | sa726dy | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197142 | 204120 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6EB | SA726EB | sa72 6eb | sa726eb | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197511 | 204212 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6ED | SA726ED | sa72 6ed | sa726ed | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197297 | 204202 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6EE | SA726EE | sa72 6ee | sa726ee | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197403 | 204168 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6EF | SA726EF | sa72 6ef | sa726ef | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197556 | 204125 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6EH | SA726EH | sa72 6eh | sa726eh | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197264 | 203938 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6EJ | SA726EJ | sa72 6ej | sa726ej | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197248 | 203965 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6EL | SA726EL | sa72 6el | sa726el | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197234 | 203910 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6EN | SA726EN | sa72 6en | sa726en | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197152 | 203829 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6EP | SA726EP | sa72 6ep | sa726ep | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196857 | 203596 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6EQ | SA726EQ | sa72 6eq | sa726eq | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197404 | 203988 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6EU | SA726EU | sa72 6eu | sa726eu | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197378 | 204081 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6EW | SA726EW | sa72 6ew | sa726ew | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197273 | 203840 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6EZ | SA726EZ | sa72 6ez | sa726ez | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197236 | 204036 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6FB | SA726FB | sa72 6fb | sa726fb | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197186 | 204205 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6FD | SA726FD | sa72 6fd | sa726fd | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197526 | 204426 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6GL | SA726GL | sa72 6gl | sa726gl | Pembrokeshire |  | Pembroke Dock |  | 1121 | 900-1200 | 2.2437 | 1.6417 | 1.2039 | 20.8937 | 11.1433 | 12.3163 | 194719 | 202967 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HA | SA726HA | sa72 6ha | sa726ha | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196995 | 203537 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HB | SA726HB | sa72 6hb | sa726hb | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196967 | 203409 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HD | SA726HD | sa72 6hd | sa726hd | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196918 | 203175 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HE | SA726HE | sa72 6he | sa726he | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196940 | 203166 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HF | SA726HF | sa72 6hf | sa726hf | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 197009 | 203475 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HG | SA726HG | sa72 6hg | sa726hg | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196995 | 203293 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HH | SA726HH | sa72 6hh | sa726hh | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196987 | 203394 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HJ | SA726HJ | sa72 6hj | sa726hj | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197057 | 203487 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HL | SA726HL | sa72 6hl | sa726hl | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197072 | 203384 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HN | SA726HN | sa72 6hn | sa726hn | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197126 | 203496 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HP | SA726HP | sa72 6hp | sa726hp | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197165 | 203412 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HQ | SA726HQ | sa72 6hq | sa726hq | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197159 | 203278 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HR | SA726HR | sa72 6hr | sa726hr | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197223 | 203401 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HS | SA726HS | sa72 6hs | sa726hs | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197380 | 203307 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HT | SA726HT | sa72 6ht | sa726ht | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197361 | 203351 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HU | SA726HU | sa72 6hu | sa726hu | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197302 | 203344 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HW | SA726HW | sa72 6hw | sa726hw | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197386 | 203425 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6HZ | SA726HZ | sa72 6hz | sa726hz | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197190 | 204113 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JA | SA726JA | sa72 6ja | sa726ja | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196788 | 203564 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JD | SA726JD | sa72 6jd | sa726jd | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196760 | 203640 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JE | SA726JE | sa72 6je | sa726je | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196662 | 203574 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JF | SA726JF | sa72 6jf | sa726jf | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196581 | 203585 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JG | SA726JG | sa72 6jg | sa726jg | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196595 | 203469 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JH | SA726JH | sa72 6jh | sa726jh | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196482 | 203578 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JJ | SA726JJ | sa72 6jj | sa726jj | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196499 | 203551 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JL | SA726JL | sa72 6jl | sa726jl | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196403 | 203597 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JN | SA726JN | sa72 6jn | sa726jn | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196352 | 203479 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JP | SA726JP | sa72 6jp | sa726jp | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196414 | 203497 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JQ | SA726JQ | sa72 6jq | sa726jq | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196623 | 203410 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JR | SA726JR | sa72 6jr | sa726jr | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196453 | 203472 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JS | SA726JS | sa72 6js | sa726js | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196516 | 203478 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JT | SA726JT | sa72 6jt | sa726jt | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196500 | 203627 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JU | SA726JU | sa72 6ju | sa726ju | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196396 | 203644 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JW | SA726JW | sa72 6jw | sa726jw | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196564 | 203460 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JX | SA726JX | sa72 6jx | sa726jx | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196495 | 203738 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JY | SA726JY | sa72 6jy | sa726jy | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196658 | 203695 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6JZ | SA726JZ | sa72 6jz | sa726jz | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196713 | 203667 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LA | SA726LA | sa72 6la | sa726la | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196354 | 203525 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LE | SA726LE | sa72 6le | sa726le | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197312 | 203251 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LF | SA726LF | sa72 6lf | sa726lf | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197328 | 203198 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LG | SA726LG | sa72 6lg | sa726lg | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197312 | 203116 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LH | SA726LH | sa72 6lh | sa726lh | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197479 | 203110 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LJ | SA726LJ | sa72 6lj | sa726lj | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197494 | 203071 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LL | SA726LL | sa72 6ll | sa726ll | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197408 | 203061 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LN | SA726LN | sa72 6ln | sa726ln | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197491 | 203151 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LP | SA726LP | sa72 6lp | sa726lp | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197646 | 203071 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LQ | SA726LQ | sa72 6lq | sa726lq | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197220 | 203179 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LR | SA726LR | sa72 6lr | sa726lr | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197599 | 203230 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LS | SA726LS | sa72 6ls | sa726ls | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197652 | 203219 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LT | SA726LT | sa72 6lt | sa726lt | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197732 | 203308 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LU | SA726LU | sa72 6lu | sa726lu | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197788 | 203265 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LW | SA726LW | sa72 6lw | sa726lw | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197544 | 203179 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LX | SA726LX | sa72 6lx | sa726lx | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197718 | 203202 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LY | SA726LY | sa72 6ly | sa726ly | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197669 | 203147 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6LZ | SA726LZ | sa72 6lz | sa726lz | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197746 | 203158 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NA | SA726NA | sa72 6na | sa726na | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197648 | 203149 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NB | SA726NB | sa72 6nb | sa726nb | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197819 | 203180 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6ND | SA726ND | sa72 6nd | sa726nd | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197874 | 203062 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NE | SA726NE | sa72 6ne | sa726ne | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197758 | 203044 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NG | SA726NG | sa72 6ng | sa726ng | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197711 | 203093 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NL | SA726NL | sa72 6nl | sa726nl | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196375 | 203089 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NN | SA726NN | sa72 6nn | sa726nn | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196315 | 203035 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NP | SA726NP | sa72 6np | sa726np | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196299 | 202985 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NR | SA726NR | sa72 6nr | sa726nr | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196174 | 203046 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NS | SA726NS | sa72 6ns | sa726ns | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196202 | 203074 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NT | SA726NT | sa72 6nt | sa726nt | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196075 | 203112 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NU | SA726NU | sa72 6nu | sa726nu | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196191 | 202954 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NW | SA726NW | sa72 6nw | sa726nw | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196343 | 202830 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NX | SA726NX | sa72 6nx | sa726nx | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196295 | 202882 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NY | SA726NY | sa72 6ny | sa726ny | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196314 | 202853 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6NZ | SA726NZ | sa72 6nz | sa726nz | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196271 | 202797 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PA | SA726PA | sa72 6pa | sa726pa | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196459 | 202971 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PB | SA726PB | sa72 6pb | sa726pb | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196668 | 202928 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PD | SA726PD | sa72 6pd | sa726pd | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196771 | 202834 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PE | SA726PE | sa72 6pe | sa726pe | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196803 | 202921 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PF | SA726PF | sa72 6pf | sa726pf | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196570 | 202892 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PG | SA726PG | sa72 6pg | sa726pg | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 197007 | 202925 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PH | SA726PH | sa72 6ph | sa726ph | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196806 | 202886 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PJ | SA726PJ | sa72 6pj | sa726pj | Pembrokeshire |  | Pembroke Dock |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 197065 | 202866 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PL | SA726PL | sa72 6pl | sa726pl | Pembrokeshire |  | Pembroke Dock |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 197065 | 202795 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PN | SA726PN | sa72 6pn | sa726pn | Pembrokeshire |  | Pembroke Dock |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 197270 | 202568 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PP | SA726PP | sa72 6pp | sa726pp | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196257 | 202752 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PQ | SA726PQ | sa72 6pq | sa726pq | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196923 | 202876 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PR | SA726PR | sa72 6pr | sa726pr | Pembrokeshire |  | Pembroke Dock |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 197144 | 202723 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PS | SA726PS | sa72 6ps | sa726ps | Pembrokeshire |  | Pembroke Dock |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 197124 | 202682 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PT | SA726PT | sa72 6pt | sa726pt | Pembrokeshire |  | Pembroke Dock |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 197149 | 202635 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PW | SA726PW | sa72 6pw | sa726pw | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196970 | 202764 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6PZ | SA726PZ | sa72 6pz | sa726pz | Pembrokeshire |  | Pembroke Dock |  | 1207 | 1200-1500 | 2.4159 | 1.7677 | 1.2963 | 22.4966 | 11.9982 | 13.2611 | 197116 | 202576 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QD | SA726QD | sa72 6qd | sa726qd | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196810 | 202561 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QE | SA726QE | sa72 6qe | sa726qe | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196775 | 202690 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QF | SA726QF | sa72 6qf | sa726qf | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196901 | 202688 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QH | SA726QH | sa72 6qh | sa726qh | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196669 | 202683 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QJ | SA726QJ | sa72 6qj | sa726qj | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196623 | 202733 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QL | SA726QL | sa72 6ql | sa726ql | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196474 | 202755 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QN | SA726QN | sa72 6qn | sa726qn | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196436 | 202695 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QP | SA726QP | sa72 6qp | sa726qp | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196388 | 202800 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QQ | SA726QQ | sa72 6qq | sa726qq | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196865 | 202734 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QR | SA726QR | sa72 6qr | sa726qr | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196381 | 202893 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QS | SA726QS | sa72 6qs | sa726qs | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196451 | 202847 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QT | SA726QT | sa72 6qt | sa726qt | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196614 | 202811 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QU | SA726QU | sa72 6qu | sa726qu | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196638 | 202789 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QW | SA726QW | sa72 6qw | sa726qw | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196555 | 202602 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QX | SA726QX | sa72 6qx | sa726qx | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196877 | 202766 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QY | SA726QY | sa72 6qy | sa726qy | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196656 | 202605 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6QZ | SA726QZ | sa72 6qz | sa726qz | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196864 | 202526 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RA | SA726RA | sa72 6ra | sa726ra | Pembrokeshire |  | Pembroke Dock |  | 1121 | 900-1200 | 2.2437 | 1.6417 | 1.2039 | 20.8937 | 11.1433 | 12.3163 | 194587 | 202963 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RB | SA726RB | sa72 6rb | sa726rb | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196161 | 202286 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RD | SA726RD | sa72 6rd | sa726rd | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196186 | 202252 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RE | SA726RE | sa72 6re | sa726re | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196361 | 202206 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RF | SA726RF | sa72 6rf | sa726rf | Pembrokeshire |  | Pembroke Dock |  | 1121 | 900-1200 | 2.2437 | 1.6417 | 1.2039 | 20.8937 | 11.1433 | 12.3163 | 194678 | 202906 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RG | SA726RG | sa72 6rg | sa726rg | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196378 | 202132 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RH | SA726RH | sa72 6rh | sa726rh | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196304 | 202254 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RJ | SA726RJ | sa72 6rj | sa726rj | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196361 | 202304 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RL | SA726RL | sa72 6rl | sa726rl | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196278 | 202356 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RN | SA726RN | sa72 6rn | sa726rn | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196325 | 202427 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RP | SA726RP | sa72 6rp | sa726rp | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196269 | 202481 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RQ | SA726RQ | sa72 6rq | sa726rq | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196112 | 202586 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RR | SA726RR | sa72 6rr | sa726rr | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196223 | 202434 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RS | SA726RS | sa72 6rs | sa726rs | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196138 | 202362 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RT | SA726RT | sa72 6rt | sa726rt | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196243 | 202541 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RU | SA726RU | sa72 6ru | sa726ru | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196161 | 202503 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RW | SA726RW | sa72 6rw | sa726rw | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196196 | 202548 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RX | SA726RX | sa72 6rx | sa726rx | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195937 | 202586 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RY | SA726RY | sa72 6ry | sa726ry | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195919 | 202547 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6RZ | SA726RZ | sa72 6rz | sa726rz | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195545 | 202637 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SA | SA726SA | sa72 6sa | sa726sa | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195749 | 202659 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SB | SA726SB | sa72 6sb | sa726sb | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195640 | 202646 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SD | SA726SD | sa72 6sd | sa726sd | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195684 | 202674 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SE | SA726SE | sa72 6se | sa726se | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195520 | 202741 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SF | SA726SF | sa72 6sf | sa726sf | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195727 | 202695 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SG | SA726SG | sa72 6sg | sa726sg | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195870 | 202682 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SH | SA726SH | sa72 6sh | sa726sh | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196188 | 202631 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SJ | SA726SJ | sa72 6sj | sa726sj | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196159 | 202711 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SL | SA726SL | sa72 6sl | sa726sl | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195964 | 202786 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SN | SA726SN | sa72 6sn | sa726sn | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196187 | 202883 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SP | SA726SP | sa72 6sp | sa726sp | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196097 | 202718 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SQ | SA726SQ | sa72 6sq | sa726sq | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196048 | 202639 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SR | SA726SR | sa72 6sr | sa726sr | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196119 | 202823 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SS | SA726SS | sa72 6ss | sa726ss | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196190 | 202766 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6ST | SA726ST | sa72 6st | sa726st | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195998 | 202715 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SW | SA726SW | sa72 6sw | sa726sw | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196045 | 202929 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SX | SA726SX | sa72 6sx | sa726sx | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195858 | 203495 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SY | SA726SY | sa72 6sy | sa726sy | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195752 | 203509 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6SZ | SA726SZ | sa72 6sz | sa726sz | Pembrokeshire |  | Pembroke Dock |  | 1167 | 900-1200 | 2.3358 | 1.7091 | 1.2534 | 21.751 | 11.6006 | 12.8217 | 195723 | 202748 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TA | SA726TA | sa72 6ta | sa726ta | Pembrokeshire |  | Pembroke Dock |  | 1187 | 900-1200 | 2.3758 | 1.7384 | 1.2748 | 22.1238 | 11.7994 | 13.0414 | 196220 | 202697 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TD | SA726TD | sa72 6td | sa726td | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196037 | 203636 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TE | SA726TE | sa72 6te | sa726te | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195900 | 203890 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TG | SA726TG | sa72 6tg | sa726tg | Pembrokeshire |  | Pembroke Dock |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196984 | 204159 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TH | SA726TH | sa72 6th | sa726th | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195663 | 203925 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TJ | SA726TJ | sa72 6tj | sa726tj | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195827 | 203351 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TL | SA726TL | sa72 6tl | sa726tl | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195553 | 203311 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TN | SA726TN | sa72 6tn | sa726tn | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195472 | 203320 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TP | SA726TP | sa72 6tp | sa726tp | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195340 | 203310 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TQ | SA726TQ | sa72 6tq | sa726tq | Pembrokeshire |  | Pembroke Dock |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196934 | 204038 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TR | SA726TR | sa72 6tr | sa726tr | Pembrokeshire |  | Pembroke Dock |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196835 | 204041 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TU | SA726TU | sa72 6tu | sa726tu | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197719 | 203540 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TX | SA726TX | sa72 6tx | sa726tx | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197647 | 203524 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TY | SA726TY | sa72 6ty | sa726ty | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197680 | 203622 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6TZ | SA726TZ | sa72 6tz | sa726tz | Pembrokeshire |  | Pembroke Dock |  | 1198 | 900-1200 | 2.3978 | 1.7545 | 1.2866 | 22.3288 | 11.9087 | 13.1623 | 197056 | 204054 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6UA | SA726UA | sa72 6ua | sa726ua | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197610 | 203852 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6UB | SA726UB | sa72 6ub | sa726ub | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197711 | 203814 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6UF | SA726UF | sa72 6uf | sa726uf | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196084 | 203867 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6UG | SA726UG | sa72 6ug | sa726ug | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197603 | 203455 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6UJ | SA726UJ | sa72 6uj | sa726uj | Pembrokeshire |  | Pembroke Dock |  | 1181 | 900-1200 | 2.3638 | 1.7296 | 1.2684 | 22.012 | 11.7397 | 12.9755 | 198172 | 204083 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6UL | SA726UL | sa72 6ul | sa726ul | Pembrokeshire |  | Pembroke Dock |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196780 | 204008 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6UN | SA726UN | sa72 6un | sa726un | Pembrokeshire |  | Pembroke Dock |  | 1181 | 900-1200 | 2.3638 | 1.7296 | 1.2684 | 22.012 | 11.7397 | 12.9755 | 198021 | 204225 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6UQ | SA726UQ | sa72 6uq | sa726uq | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197629 | 203379 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6UR | SA726UR | sa72 6ur | sa726ur | Pembrokeshire |  | Pembroke Dock |  | 1185 | 900-1200 | 2.3718 | 1.7355 | 1.2727 | 22.0865 | 11.7795 | 13.0194 | 197445 | 203805 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6UT | SA726UT | sa72 6ut | sa726ut | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196688 | 203420 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6UU | SA726UU | sa72 6uu | sa726uu | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196658 | 203293 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6WS | SA726WS | sa72 6ws | sa726ws | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196240 | 203555 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6WT | SA726WT | sa72 6wt | sa726wt | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196060 | 203730 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6WX | SA726WX | sa72 6wx | sa726wx | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195812 | 203716 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XB | SA726XB | sa72 6xb | sa726xb | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196526 | 203387 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XD | SA726XD | sa72 6xd | sa726xd | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196619 | 203366 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XE | SA726XE | sa72 6xe | sa726xe | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196381 | 203432 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XF | SA726XF | sa72 6xf | sa726xf | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196385 | 203362 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XH | SA726XH | sa72 6xh | sa726xh | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196304 | 203316 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XJ | SA726XJ | sa72 6xj | sa726xj | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196282 | 203231 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XL | SA726XL | sa72 6xl | sa726xl | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196345 | 203387 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XN | SA726XN | sa72 6xn | sa726xn | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196246 | 203246 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XP | SA726XP | sa72 6xp | sa726xp | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196229 | 203322 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XQ | SA726XQ | sa72 6xq | sa726xq | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195666 | 203402 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XS | SA726XS | sa72 6xs | sa726xs | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196147 | 203397 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XT | SA726XT | sa72 6xt | sa726xt | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196129 | 203355 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XU | SA726XU | sa72 6xu | sa726xu | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196160 | 203278 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XW | SA726XW | sa72 6xw | sa726xw | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195593 | 203492 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6XX | SA726XX | sa72 6xx | sa726xx | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 196016 | 203332 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6YA | SA726YA | sa72 6ya | sa726ya | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196074 | 203358 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6YB | SA726YB | sa72 6yb | sa726yb | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196038 | 203427 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6YD | SA726YD | sa72 6yd | sa726yd | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196031 | 203390 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6YE | SA726YE | sa72 6ye | sa726ye | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195887 | 203380 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6YG | SA726YG | sa72 6yg | sa726yg | Pembrokeshire |  | Pembroke Dock |  | 1153 | 900-1200 | 2.3078 | 1.6886 | 1.2383 | 21.4901 | 11.4614 | 12.6679 | 195984 | 203348 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA72 6YH | SA726YH | sa72 6yh | sa726yh | Pembrokeshire |  | Pembroke Dock |  | 1170 | 900-1200 | 2.3418 | 1.7135 | 1.2566 | 21.807 | 11.6304 | 12.8546 | 196112 | 203489 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AA | SA731AA | sa73 1aa | sa731aa | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191271 | 206725 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AB | SA731AB | sa73 1ab | sa731ab | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191327 | 206722 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AD | SA731AD | sa73 1ad | sa731ad | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191343 | 207051 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AE | SA731AE | sa73 1ae | sa731ae | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191299 | 207158 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AF | SA731AF | sa73 1af | sa731af | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191265 | 207030 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AG | SA731AG | sa73 1ag | sa731ag | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191394 | 207013 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AH | SA731AH | sa73 1ah | sa731ah | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191496 | 207216 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AJ | SA731AJ | sa73 1aj | sa731aj | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191589 | 207487 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AL | SA731AL | sa73 1al | sa731al | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191665 | 207614 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AN | SA731AN | sa73 1an | sa731an | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191696 | 207552 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AP | SA731AP | sa73 1ap | sa731ap | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191784 | 207752 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AQ | SA731AQ | sa73 1aq | sa731aq | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191419 | 206979 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AR | SA731AR | sa73 1ar | sa731ar | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191570 | 207601 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AS | SA731AS | sa73 1as | sa731as | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191686 | 207321 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AT | SA731AT | sa73 1at | sa731at | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190966 | 206406 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AU | SA731AU | sa73 1au | sa731au | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191592 | 207125 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AW | SA731AW | sa73 1aw | sa731aw | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191753 | 207804 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AX | SA731AX | sa73 1ax | sa731ax | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191650 | 207360 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AY | SA731AY | sa73 1ay | sa731ay | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191577 | 207162 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1AZ | SA731AZ | sa73 1az | sa731az | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191678 | 207102 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BA | SA731BA | sa73 1ba | sa731ba | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191049 | 206477 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BB | SA731BB | sa73 1bb | sa731bb | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191227 | 206449 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BD | SA731BD | sa73 1bd | sa731bd | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191182 | 206390 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BE | SA731BE | sa73 1be | sa731be | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191233 | 206375 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BG | SA731BG | sa73 1bg | sa731bg | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191223 | 206516 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BH | SA731BH | sa73 1bh | sa731bh | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191117 | 206639 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BJ | SA731BJ | sa73 1bj | sa731bj | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191184 | 206622 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BL | SA731BL | sa73 1bl | sa731bl | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191171 | 206809 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BN | SA731BN | sa73 1bn | sa731bn | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191283 | 206388 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BP | SA731BP | sa73 1bp | sa731bp | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191364 | 206412 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BQ | SA731BQ | sa73 1bq | sa731bq | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191316 | 206518 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BR | SA731BR | sa73 1br | sa731br | Pembrokeshire |  | Waterston |  | 1137 | 900-1200 | 2.2757 | 1.6652 | 1.2211 | 21.1919 | 11.3023 | 12.4921 | 193537 | 205863 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BS | SA731BS | sa73 1bs | sa731bs | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191441 | 206382 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BT | SA731BT | sa73 1bt | sa731bt | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191313 | 206597 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BU | SA731BU | sa73 1bu | sa731bu | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191226 | 206586 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BW | SA731BW | sa73 1bw | sa731bw | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191334 | 206407 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BX | SA731BX | sa73 1bx | sa731bx | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191389 | 206487 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BY | SA731BY | sa73 1by | sa731by | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191421 | 206564 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1BZ | SA731BZ | sa73 1bz | sa731bz | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191416 | 206290 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DA | SA731DA | sa73 1da | sa731da | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191116 | 206427 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DB | SA731DB | sa73 1db | sa731db | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191477 | 206160 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DD | SA731DD | sa73 1dd | sa731dd | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191255 | 206304 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DE | SA731DE | sa73 1de | sa731de | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191531 | 206126 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DF | SA731DF | sa73 1df | sa731df | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191363 | 206725 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DG | SA731DG | sa73 1dg | sa731dg | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191677 | 206042 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DJ | SA731DJ | sa73 1dj | sa731dj | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191734 | 205927 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DL | SA731DL | sa73 1dl | sa731dl | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191914 | 206041 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DN | SA731DN | sa73 1dn | sa731dn | Pembrokeshire |  | Milford Haven |  | 1087 | 900-1200 | 2.1757 | 1.592 | 1.1674 | 20.26 | 10.8053 | 11.9427 | 192726 | 206005 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DP | SA731DP | sa73 1dp | sa731dp | Pembrokeshire |  | Waterston |  | 1137 | 900-1200 | 2.2757 | 1.6652 | 1.2211 | 21.1919 | 11.3023 | 12.4921 | 193360 | 205883 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DR | SA731DR | sa73 1dr | sa731dr | Pembrokeshire |  | Waterston |  | 1137 | 900-1200 | 2.2757 | 1.6652 | 1.2211 | 21.1919 | 11.3023 | 12.4921 | 193675 | 205597 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DS | SA731DS | sa73 1ds | sa731ds | Pembrokeshire |  | Waterston |  | 1137 | 900-1200 | 2.2757 | 1.6652 | 1.2211 | 21.1919 | 11.3023 | 12.4921 | 193609 | 205933 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DT | SA731DT | sa73 1dt | sa731dt | Pembrokeshire |  | Waterston |  | 1137 | 900-1200 | 2.2757 | 1.6652 | 1.2211 | 21.1919 | 11.3023 | 12.4921 | 193667 | 205847 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DU | SA731DU | sa73 1du | sa731du | Pembrokeshire |  | Waterston |  | 1137 | 900-1200 | 2.2757 | 1.6652 | 1.2211 | 21.1919 | 11.3023 | 12.4921 | 193754 | 205774 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DW | SA731DW | sa73 1dw | sa731dw | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191698 | 207246 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DX | SA731DX | sa73 1dx | sa731dx | Pembrokeshire |  | Waterston |  | 1137 | 900-1200 | 2.2757 | 1.6652 | 1.2211 | 21.1919 | 11.3023 | 12.4921 | 193789 | 205708 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DY | SA731DY | sa73 1dy | sa731dy | Pembrokeshire |  | Waterston |  | 1137 | 900-1200 | 2.2757 | 1.6652 | 1.2211 | 21.1919 | 11.3023 | 12.4921 | 193851 | 205719 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1DZ | SA731DZ | sa73 1dz | sa731dz | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191731 | 207125 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EA | SA731EA | sa73 1ea | sa731ea | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195707 | 205081 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EB | SA731EB | sa73 1eb | sa731eb | Pembrokeshire |  | Neyland |  | 1132 | 900-1200 | 2.2657 | 1.6579 | 1.2158 | 21.0987 | 11.2526 | 12.4371 | 195174 | 204935 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1ED | SA731ED | sa73 1ed | sa731ed | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195900 | 205473 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EE | SA731EE | sa73 1ee | sa731ee | Pembrokeshire |  | Neyland |  | 1117 | 900-1200 | 2.2357 | 1.6359 | 1.1997 | 20.8191 | 11.1035 | 12.2723 | 194839 | 204886 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EF | SA731EF | sa73 1ef | sa731ef | Pembrokeshire |  | Neyland |  | 1117 | 900-1200 | 2.2357 | 1.6359 | 1.1997 | 20.8191 | 11.1035 | 12.2723 | 194608 | 204786 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EG | SA731EG | sa73 1eg | sa731eg | Pembrokeshire |  | Neyland |  | 1117 | 900-1200 | 2.2357 | 1.6359 | 1.1997 | 20.8191 | 11.1035 | 12.2723 | 194746 | 204767 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EH | SA731EH | sa73 1eh | sa731eh | Pembrokeshire |  | Neyland |  | 1117 | 900-1200 | 2.2357 | 1.6359 | 1.1997 | 20.8191 | 11.1035 | 12.2723 | 194664 | 204842 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EH | SA731EH | sa73 1eh | sa731eh | Pembrokeshire |  | Waterston |  | 1117 | 900-1200 | 2.2357 | 1.6359 | 1.1997 | 20.8191 | 11.1035 | 12.2723 | 194664 | 204842 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EJ | SA731EJ | sa73 1ej | sa731ej | Pembrokeshire |  | Waterston |  | 1117 | 900-1200 | 2.2357 | 1.6359 | 1.1997 | 20.8191 | 11.1035 | 12.2723 | 194449 | 204910 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EL | SA731EL | sa73 1el | sa731el | Pembrokeshire |  | Neyland |  | 1168 | 900-1200 | 2.3378 | 1.7106 | 1.2544 | 21.7697 | 11.6105 | 12.8327 | 194860 | 205202 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EL | SA731EL | sa73 1el | sa731el | Pembrokeshire |  | Waterston |  | 1168 | 900-1200 | 2.3378 | 1.7106 | 1.2544 | 21.7697 | 11.6105 | 12.8327 | 194860 | 205202 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EN | SA731EN | sa73 1en | sa731en | Pembrokeshire |  | Neyland |  | 1168 | 900-1200 | 2.3378 | 1.7106 | 1.2544 | 21.7697 | 11.6105 | 12.8327 | 194922 | 205071 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EP | SA731EP | sa73 1ep | sa731ep | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195073 | 205586 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1ER | SA731ER | sa73 1er | sa731er | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195437 | 205653 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1ET | SA731ET | sa73 1et | sa731et | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191840 | 205976 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EU | SA731EU | sa73 1eu | sa731eu | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191687 | 205952 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EW | SA731EW | sa73 1ew | sa731ew | Pembrokeshire |  | Neyland |  | 1168 | 900-1200 | 2.3378 | 1.7106 | 1.2544 | 21.7697 | 11.6105 | 12.8327 | 194783 | 204997 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EX | SA731EX | sa73 1ex | sa731ex | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191605 | 206909 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EY | SA731EY | sa73 1ey | sa731ey | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191456 | 206216 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1EZ | SA731EZ | sa73 1ez | sa731ez | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191439 | 206457 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1FA | SA731FA | sa73 1fa | sa731fa | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195462 | 205594 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1FB | SA731FB | sa73 1fb | sa731fb | Pembrokeshire |  | Neyland |  | 1179 | 900-1200 | 2.3598 | 1.7267 | 1.2662 | 21.9747 | 11.7198 | 12.9535 | 195897 | 206626 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1GA | SA731GA | sa73 1ga | sa731ga | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196242 | 205532 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1GB | SA731GB | sa73 1gb | sa731gb | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191797 | 207199 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1GH | SA731GH | sa73 1gh | sa731gh | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191587 | 207002 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1GL | SA731GL | sa73 1gl | sa731gl | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191621 | 206962 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1HB | SA731HB | sa73 1hb | sa731hb | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191725 | 207495 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1HD | SA731HD | sa73 1hd | sa731hd | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191830 | 207589 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1HE | SA731HE | sa73 1he | sa731he | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191842 | 207239 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1HF | SA731HF | sa73 1hf | sa731hf | Pembrokeshire |  | Milford Haven |  | 1114 | 900-1200 | 2.2297 | 1.6315 | 1.1964 | 20.7632 | 11.0737 | 12.2394 | 192072 | 207626 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1HG | SA731HG | sa73 1hg | sa731hg | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191827 | 207702 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1HH | SA731HH | sa73 1hh | sa731hh | Pembrokeshire |  | Milford Haven |  | 1114 | 900-1200 | 2.2297 | 1.6315 | 1.1964 | 20.7632 | 11.0737 | 12.2394 | 192049 | 207783 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1HQ | SA731HQ | sa73 1hq | sa731hq | Pembrokeshire |  | Milford Haven |  | 1114 | 900-1200 | 2.2297 | 1.6315 | 1.1964 | 20.7632 | 11.0737 | 12.2394 | 192145 | 207657 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1HT | SA731HT | sa73 1ht | sa731ht | Pembrokeshire |  | Milford Haven |  | 1114 | 900-1200 | 2.2297 | 1.6315 | 1.1964 | 20.7632 | 11.0737 | 12.2394 | 192222 | 207656 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1HY | SA731HY | sa73 1hy | sa731hy | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191931 | 207726 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1HZ | SA731HZ | sa73 1hz | sa731hz | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191960 | 207631 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JA | SA731JA | sa73 1ja | sa731ja | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191948 | 207576 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JB | SA731JB | sa73 1jb | sa731jb | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 192016 | 207683 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JG | SA731JG | sa73 1jg | sa731jg | Pembrokeshire |  | Rosemarket |  | 1162 | 900-1200 | 2.3258 | 1.7018 | 1.248 | 21.6579 | 11.5509 | 12.7667 | 195289 | 208181 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JH | SA731JH | sa73 1jh | sa731jh | Pembrokeshire |  | Rosemarket |  | 1162 | 900-1200 | 2.3258 | 1.7018 | 1.248 | 21.6579 | 11.5509 | 12.7667 | 195159 | 208323 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JL | SA731JL | sa73 1jl | sa731jl | Pembrokeshire |  | Rosemarket |  | 1162 | 900-1200 | 2.3258 | 1.7018 | 1.248 | 21.6579 | 11.5509 | 12.7667 | 195186 | 208522 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JN | SA731JN | sa73 1jn | sa731jn | Pembrokeshire |  | Milford Haven |  | 1114 | 900-1200 | 2.2297 | 1.6315 | 1.1964 | 20.7632 | 11.0737 | 12.2394 | 192043 | 207608 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JP | SA731JP | sa73 1jp | sa731jp | Pembrokeshire |  | Rosemarket |  | 1162 | 900-1200 | 2.3258 | 1.7018 | 1.248 | 21.6579 | 11.5509 | 12.7667 | 195277 | 208404 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JQ | SA731JQ | sa73 1jq | sa731jq | Pembrokeshire |  | Rosemarket |  | 1162 | 900-1200 | 2.3258 | 1.7018 | 1.248 | 21.6579 | 11.5509 | 12.7667 | 195499 | 208596 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JR | SA731JR | sa73 1jr | sa731jr | Pembrokeshire |  | Rosemarket |  | 1162 | 900-1200 | 2.3258 | 1.7018 | 1.248 | 21.6579 | 11.5509 | 12.7667 | 195316 | 208506 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JS | SA731JS | sa73 1js | sa731js | Pembrokeshire |  | Rosemarket |  | 1162 | 900-1200 | 2.3258 | 1.7018 | 1.248 | 21.6579 | 11.5509 | 12.7667 | 195306 | 208287 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JT | SA731JT | sa73 1jt | sa731jt | Pembrokeshire |  | Rosemarket |  | 1162 | 900-1200 | 2.3258 | 1.7018 | 1.248 | 21.6579 | 11.5509 | 12.7667 | 195357 | 208452 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JU | SA731JU | sa73 1ju | sa731ju | Pembrokeshire |  | Rosemarket |  | 1162 | 900-1200 | 2.3258 | 1.7018 | 1.248 | 21.6579 | 11.5509 | 12.7667 | 195321 | 208567 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JW | SA731JW | sa73 1jw | sa731jw | Pembrokeshire |  | Rosemarket |  | 1162 | 900-1200 | 2.3258 | 1.7018 | 1.248 | 21.6579 | 11.5509 | 12.7667 | 195439 | 208514 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1JX | SA731JX | sa73 1jx | sa731jx | Pembrokeshire |  | Rosemarket |  | 1162 | 900-1200 | 2.3258 | 1.7018 | 1.248 | 21.6579 | 11.5509 | 12.7667 | 195260 | 208739 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LA | SA731LA | sa73 1la | sa731la | Pembrokeshire |  | Llangwm |  | 1211 | 1200-1500 | 2.4239 | 1.7736 | 1.3006 | 22.5711 | 12.0379 | 13.3051 | 197012 | 208650 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LG | SA731LG | sa73 1lg | sa731lg | Pembrokeshire |  | Neyland |  | 1211 | 1200-1500 | 2.4239 | 1.7736 | 1.3006 | 22.5711 | 12.0379 | 13.3051 | 197144 | 206656 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LR | SA731LR | sa73 1lr | sa731lr | Pembrokeshire |  | Burton Ferry |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 198376 | 205550 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LS | SA731LS | sa73 1ls | sa731ls | Pembrokeshire |  | Neyland |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196544 | 204846 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LU | SA731LU | sa73 1lu | sa731lu | Pembrokeshire |  | Llangwm |  | 1211 | 1200-1500 | 2.4239 | 1.7736 | 1.3006 | 22.5711 | 12.0379 | 13.3051 | 196907 | 208807 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LW | SA731LW | sa73 1lw | sa731lw | Pembrokeshire |  | Burton Ferry |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 198540 | 205429 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LX | SA731LX | sa73 1lx | sa731lx | Pembrokeshire |  | Llangwm |  | 1246 | 1200-1500 | 2.4939 | 1.8248 | 1.3382 | 23.2235 | 12.3859 | 13.6896 | 197043 | 208762 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LY | SA731LY | sa73 1ly | sa731ly | Pembrokeshire |  | Llangwm |  | 1246 | 1200-1500 | 2.4939 | 1.8248 | 1.3382 | 23.2235 | 12.3859 | 13.6896 | 197251 | 208602 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1LZ | SA731LZ | sa73 1lz | sa731lz | Pembrokeshire |  | Llangwm |  | 1246 | 1200-1500 | 2.4939 | 1.8248 | 1.3382 | 23.2235 | 12.3859 | 13.6896 | 197039 | 208805 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NA | SA731NA | sa73 1na | sa731na | Pembrokeshire |  | Llangwm |  | 1246 | 1200-1500 | 2.4939 | 1.8248 | 1.3382 | 23.2235 | 12.3859 | 13.6896 | 197552 | 208415 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NB | SA731NB | sa73 1nb | sa731nb | Pembrokeshire |  | Llangwm |  | 1246 | 1200-1500 | 2.4939 | 1.8248 | 1.3382 | 23.2235 | 12.3859 | 13.6896 | 197878 | 208278 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1ND | SA731ND | sa73 1nd | sa731nd | Pembrokeshire |  | Llangwm |  | 1250 | 1200-1500 | 2.5019 | 1.8307 | 1.3425 | 23.298 | 12.4256 | 13.7336 | 198276 | 208005 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NE | SA731NE | sa73 1ne | sa731ne | Pembrokeshire |  | Llangwm |  | 1252 | 1200-1500 | 2.5059 | 1.8336 | 1.3446 | 23.3353 | 12.4455 | 13.7556 | 198272 | 207756 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NG | SA731NG | sa73 1ng | sa731ng | PCNPA |  | Llangwm |  | 1250 | 1200-1500 | 2.5019 | 1.8307 | 1.3425 | 23.298 | 12.4256 | 13.7336 | 198384 | 208201 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 1NH | SA731NH | sa73 1nh | sa731nh | Pembrokeshire |  | Llangwm |  | 1250 | 1200-1500 | 2.5019 | 1.8307 | 1.3425 | 23.298 | 12.4256 | 13.7336 | 198355 | 207981 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NJ | SA731NJ | sa73 1nj | sa731nj | PCNPA |  | Llangwm |  | 1252 | 1200-1500 | 2.5059 | 1.8336 | 1.3446 | 23.3353 | 12.4455 | 13.7556 | 198505 | 207561 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 1NL | SA731NL | sa73 1nl | sa731nl | PCNPA |  | Llangwm |  | 1252 | 1200-1500 | 2.5059 | 1.8336 | 1.3446 | 23.3353 | 12.4455 | 13.7556 | 198717 | 207070 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 1NN | SA731NN | sa73 1nn | sa731nn | Pembrokeshire |  | Llangwm |  | 1252 | 1200-1500 | 2.5059 | 1.8336 | 1.3446 | 23.3353 | 12.4455 | 13.7556 | 198285 | 207376 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NP | SA731NP | sa73 1np | sa731np | Pembrokeshire |  | Llangwm |  | 1252 | 1200-1500 | 2.5059 | 1.8336 | 1.3446 | 23.3353 | 12.4455 | 13.7556 | 198359 | 207246 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NQ | SA731NQ | sa73 1nq | sa731nq | Pembrokeshire |  | Llangwm |  | 1252 | 1200-1500 | 2.5059 | 1.8336 | 1.3446 | 23.3353 | 12.4455 | 13.7556 | 198292 | 207155 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NR | SA731NR | sa73 1nr | sa731nr | Pembrokeshire |  | Llangwm |  | 1252 | 1200-1500 | 2.5059 | 1.8336 | 1.3446 | 23.3353 | 12.4455 | 13.7556 | 198342 | 207066 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NS | SA731NS | sa73 1ns | sa731ns | Pembrokeshire |  | Burton Ferry |  | 1242 | 1200-1500 | 2.4859 | 1.819 | 1.3339 | 23.1489 | 12.3461 | 13.6457 | 198223 | 206579 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NT | SA731NT | sa73 1nt | sa731nt | Pembrokeshire |  | Llangwm |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 198223 | 206579 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NU | SA731NU | sa73 1nu | sa731nu | Pembrokeshire |  | Burton Ferry |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 198335 | 205407 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NW | SA731NW | sa73 1nw | sa731nw | Pembrokeshire |  | Burton Ferry |  | 1252 | 1200-1500 | 2.5059 | 1.8336 | 1.3446 | 23.3353 | 12.4455 | 13.7556 | 198476 | 205485 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NX | SA731NX | sa73 1nx | sa731nx | Pembrokeshire |  | Llangwm |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 198316 | 207218 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NY | SA731NY | sa73 1ny | sa731ny | Pembrokeshire |  | Burton Ferry |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 198170 | 205097 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1NZ | SA731NZ | sa73 1nz | sa731nz | Pembrokeshire |  | Burton Ferry |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 198197 | 204986 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PA | SA731PA | sa73 1pa | sa731pa | Pembrokeshire |  | Burton Ferry |  | 1217 | 1200-1500 | 2.4359 | 1.7823 | 1.3071 | 22.683 | 12.0976 | 13.371 | 198520 | 205379 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PB | SA731PB | sa73 1pb | sa731pb | Pembrokeshire |  | Burton Ferry |  | 1217 | 1200-1500 | 2.4359 | 1.7823 | 1.3071 | 22.683 | 12.0976 | 13.371 | 197666 | 205253 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PF | SA731PF | sa73 1pf | sa731pf | Pembrokeshire |  | Burton Ferry |  | 1217 | 1200-1500 | 2.4359 | 1.7823 | 1.3071 | 22.683 | 12.0976 | 13.371 | 197233 | 205293 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PG | SA731PG | sa73 1pg | sa731pg | Pembrokeshire |  | Burton Ferry |  | 1232 | 1200-1500 | 2.4659 | 1.8043 | 1.3232 | 22.9625 | 12.2467 | 13.5358 | 197039 | 205300 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PH | SA731PH | sa73 1ph | sa731ph | Pembrokeshire |  | Neyland |  | 1148 | 900-1200 | 2.2978 | 1.6813 | 1.2329 | 21.3969 | 11.4117 | 12.6129 | 196363 | 206115 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PJ | SA731PJ | sa73 1pj | sa731pj | Pembrokeshire |  | Neyland |  | 1148 | 900-1200 | 2.2978 | 1.6813 | 1.2329 | 21.3969 | 11.4117 | 12.6129 | 196430 | 206096 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PL | SA731PL | sa73 1pl | sa731pl | Pembrokeshire |  | Neyland |  | 1148 | 900-1200 | 2.2978 | 1.6813 | 1.2329 | 21.3969 | 11.4117 | 12.6129 | 196504 | 206075 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PN | SA731PN | sa73 1pn | sa731pn | Pembrokeshire |  | Neyland |  | 1148 | 900-1200 | 2.2978 | 1.6813 | 1.2329 | 21.3969 | 11.4117 | 12.6129 | 196590 | 206055 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PP | SA731PP | sa73 1pp | sa731pp | Pembrokeshire |  | Neyland |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196507 | 204934 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PQ | SA731PQ | sa73 1pq | sa731pq | Pembrokeshire |  | Llangwm |  | 1252 | 1200-1500 | 2.5059 | 1.8336 | 1.3446 | 23.3353 | 12.4455 | 13.7556 | 198194 | 207362 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PR | SA731PR | sa73 1pr | sa731pr | Pembrokeshire |  | Neyland |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196463 | 204946 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PT | SA731PT | sa73 1pt | sa731pt | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196149 | 205413 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PU | SA731PU | sa73 1pu | sa731pu | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196065 | 205691 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PW | SA731PW | sa73 1pw | sa731pw | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196773 | 205551 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PX | SA731PX | sa73 1px | sa731px | Pembrokeshire |  | Neyland |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196498 | 204866 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PY | SA731PY | sa73 1py | sa731py | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196641 | 205126 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1PZ | SA731PZ | sa73 1pz | sa731pz | Pembrokeshire |  | Neyland |  | 1148 | 900-1200 | 2.2978 | 1.6813 | 1.2329 | 21.3969 | 11.4117 | 12.6129 | 196576 | 205980 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QA | SA731QA | sa73 1qa | sa731qa | Pembrokeshire |  | Neyland |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196374 | 204861 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QB | SA731QB | sa73 1qb | sa731qb | Pembrokeshire |  | Neyland |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196247 | 204907 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QD | SA731QD | sa73 1qd | sa731qd | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 196007 | 205121 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QE | SA731QE | sa73 1qe | sa731qe | Pembrokeshire |  | Neyland |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196109 | 204962 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QF | SA731QF | sa73 1qf | sa731qf | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195984 | 205085 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QG | SA731QG | sa73 1qg | sa731qg | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196122 | 205006 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QH | SA731QH | sa73 1qh | sa731qh | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196138 | 205069 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QJ | SA731QJ | sa73 1qj | sa731qj | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196046 | 205165 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QL | SA731QL | sa73 1ql | sa731ql | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195920 | 205189 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QN | SA731QN | sa73 1qn | sa731qn | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195686 | 205405 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QP | SA731QP | sa73 1qp | sa731qp | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195896 | 205560 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QQ | SA731QQ | sa73 1qq | sa731qq | Pembrokeshire |  | Neyland |  | 1148 | 900-1200 | 2.2978 | 1.6813 | 1.2329 | 21.3969 | 11.4117 | 12.6129 | 196393 | 205989 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QR | SA731QR | sa73 1qr | sa731qr | Pembrokeshire |  | Neyland |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196468 | 204785 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QS | SA731QS | sa73 1qs | sa731qs | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195415 | 205759 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QW | SA731QW | sa73 1qw | sa731qw | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195411 | 205535 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QX | SA731QX | sa73 1qx | sa731qx | Pembrokeshire |  | Neyland |  | 1179 | 900-1200 | 2.3598 | 1.7267 | 1.2662 | 21.9747 | 11.7198 | 12.9535 | 195345 | 206285 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1QY | SA731QY | sa73 1qy | sa731qy | Pembrokeshire |  | Neyland |  | 1179 | 900-1200 | 2.3598 | 1.7267 | 1.2662 | 21.9747 | 11.7198 | 12.9535 | 195479 | 206332 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RA | SA731RA | sa73 1ra | sa731ra | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196236 | 205790 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RB | SA731RB | sa73 1rb | sa731rb | Pembrokeshire |  | Neyland |  | 1148 | 900-1200 | 2.2978 | 1.6813 | 1.2329 | 21.3969 | 11.4117 | 12.6129 | 196357 | 206039 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RD | SA731RD | sa73 1rd | sa731rd | Pembrokeshire |  | Neyland |  | 1148 | 900-1200 | 2.2978 | 1.6813 | 1.2329 | 21.3969 | 11.4117 | 12.6129 | 196054 | 206159 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RE | SA731RE | sa73 1re | sa731re | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196082 | 205929 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RF | SA731RF | sa73 1rf | sa731rf | Pembrokeshire |  | Neyland |  | 1179 | 900-1200 | 2.3598 | 1.7267 | 1.2662 | 21.9747 | 11.7198 | 12.9535 | 195988 | 206076 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RG | SA731RG | sa73 1rg | sa731rg | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 196010 | 205886 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RH | SA731RH | sa73 1rh | sa731rh | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195945 | 205970 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RJ | SA731RJ | sa73 1rj | sa731rj | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196095 | 205863 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RL | SA731RL | sa73 1rl | sa731rl | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196097 | 205681 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RN | SA731RN | sa73 1rn | sa731rn | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196211 | 205567 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RP | SA731RP | sa73 1rp | sa731rp | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196095 | 205564 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RQ | SA731RQ | sa73 1rq | sa731rq | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195987 | 205586 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RR | SA731RR | sa73 1rr | sa731rr | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196118 | 205589 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RS | SA731RS | sa73 1rs | sa731rs | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196027 | 205541 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RT | SA731RT | sa73 1rt | sa731rt | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195947 | 205413 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RU | SA731RU | sa73 1ru | sa731ru | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195879 | 205393 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RX | SA731RX | sa73 1rx | sa731rx | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195859 | 205293 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RY | SA731RY | sa73 1ry | sa731ry | Pembrokeshire |  | Neyland |  | 1157 | 900-1200 | 2.3158 | 1.6945 | 1.2426 | 21.5647 | 11.5012 | 12.7118 | 195915 | 205252 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1RZ | SA731RZ | sa73 1rz | sa731rz | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196242 | 205923 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SA | SA731SA | sa73 1sa | sa731sa | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196109 | 205513 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SB | SA731SB | sa73 1sb | sa731sb | Pembrokeshire |  | Neyland |  | 1148 | 900-1200 | 2.2978 | 1.6813 | 1.2329 | 21.3969 | 11.4117 | 12.6129 | 196216 | 206137 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SD | SA731SD | sa73 1sd | sa731sd | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196202 | 205931 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SE | SA731SE | sa73 1se | sa731se | Pembrokeshire |  | Neyland |  | 1148 | 900-1200 | 2.2978 | 1.6813 | 1.2329 | 21.3969 | 11.4117 | 12.6129 | 196084 | 206360 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SF | SA731SF | sa73 1sf | sa731sf | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196372 | 205872 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SG | SA731SG | sa73 1sg | sa731sg | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196356 | 205833 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SH | SA731SH | sa73 1sh | sa731sh | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196408 | 205018 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SJ | SA731SJ | sa73 1sj | sa731sj | Pembrokeshire |  | Neyland |  | 1148 | 900-1200 | 2.2978 | 1.6813 | 1.2329 | 21.3969 | 11.4117 | 12.6129 | 196290 | 206197 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SL | SA731SL | sa73 1sl | sa731sl | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196506 | 205043 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SN | SA731SN | sa73 1sn | sa731sn | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196525 | 205062 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SP | SA731SP | sa73 1sp | sa731sp | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196577 | 205176 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SQ | SA731SQ | sa73 1sq | sa731sq | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196164 | 205815 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SR | SA731SR | sa73 1sr | sa731sr | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196580 | 205095 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SS | SA731SS | sa73 1ss | sa731ss | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196514 | 205130 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1ST | SA731ST | sa73 1st | sa731st | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196615 | 205314 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SU | SA731SU | sa73 1su | sa731su | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196538 | 205444 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SX | SA731SX | sa73 1sx | sa731sx | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196612 | 205529 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SY | SA731SY | sa73 1sy | sa731sy | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196521 | 205409 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1SZ | SA731SZ | sa73 1sz | sa731sz | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196618 | 205649 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TA | SA731TA | sa73 1ta | sa731ta | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196489 | 205362 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TB | SA731TB | sa73 1tb | sa731tb | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196547 | 205309 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TD | SA731TD | sa73 1td | sa731td | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196535 | 205226 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TE | SA731TE | sa73 1te | sa731te | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196437 | 205220 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TF | SA731TF | sa73 1tf | sa731tf | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196376 | 205275 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TG | SA731TG | sa73 1tg | sa731tg | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196421 | 205378 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TH | SA731TH | sa73 1th | sa731th | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196339 | 205434 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TJ | SA731TJ | sa73 1tj | sa731tj | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196226 | 205493 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TL | SA731TL | sa73 1tl | sa731tl | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196198 | 205418 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TN | SA731TN | sa73 1tn | sa731tn | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196147 | 205439 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TP | SA731TP | sa73 1tp | sa731tp | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196228 | 205421 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TQ | SA731TQ | sa73 1tq | sa731tq | Pembrokeshire |  | Neyland |  | 1148 | 900-1200 | 2.2978 | 1.6813 | 1.2329 | 21.3969 | 11.4117 | 12.6129 | 196221 | 206025 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TR | SA731TR | sa73 1tr | sa731tr | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196279 | 205372 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TS | SA731TS | sa73 1ts | sa731ts | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196176 | 205310 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TT | SA731TT | sa73 1tt | sa731tt | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196270 | 205257 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TU | SA731TU | sa73 1tu | sa731tu | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196218 | 205177 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TW | SA731TW | sa73 1tw | sa731tw | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196215 | 205677 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TX | SA731TX | sa73 1tx | sa731tx | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196328 | 205186 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1TY | SA731TY | sa73 1ty | sa731ty | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196279 | 205064 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1UA | SA731UA | sa73 1ua | sa731ua | Pembrokeshire |  | Neyland |  | 1151 | 900-1200 | 2.3038 | 1.6857 | 1.2362 | 21.4528 | 11.4415 | 12.6459 | 196261 | 204973 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1UB | SA731UB | sa73 1ub | sa731ub | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196164 | 205105 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1UD | SA731UD | sa73 1ud | sa731ud | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196115 | 205155 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1UE | SA731UE | sa73 1ue | sa731ue | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196059 | 205204 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1UF | SA731UF | sa73 1uf | sa731uf | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196255 | 205684 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1UG | SA731UG | sa73 1ug | sa731ug | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196064 | 205289 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1UH | SA731UH | sa73 1uh | sa731uh | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196271 | 205625 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 1UJ | SA731UJ | sa73 1uj | sa731uj | Pembrokeshire |  | Neyland |  | 1206 | 1200-1500 | 2.4139 | 1.7662 | 1.2952 | 22.4779 | 11.9882 | 13.2502 | 196050 | 205425 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AA | SA732AA | sa73 2aa | sa732aa | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190267 | 205994 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AB | SA732AB | sa73 2ab | sa732ab | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190327 | 205980 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AD | SA732AD | sa73 2ad | sa732ad | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190349 | 205944 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AE | SA732AE | sa73 2ae | sa732ae | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190283 | 205964 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AG | SA732AG | sa73 2ag | sa732ag | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190131 | 206053 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AH | SA732AH | sa73 2ah | sa732ah | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190210 | 206042 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AJ | SA732AJ | sa73 2aj | sa732aj | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190131 | 206003 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AL | SA732AL | sa73 2al | sa732al | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190159 | 206076 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AN | SA732AN | sa73 2an | sa732an | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190194 | 206126 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AP | SA732AP | sa73 2ap | sa732ap | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190288 | 206093 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AR | SA732AR | sa73 2ar | sa732ar | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190302 | 206168 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AS | SA732AS | sa73 2as | sa732as | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190323 | 206139 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AT | SA732AT | sa73 2at | sa732at | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190381 | 206226 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AU | SA732AU | sa73 2au | sa732au | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190366 | 206244 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AW | SA732AW | sa73 2aw | sa732aw | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190233 | 206133 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AX | SA732AX | sa73 2ax | sa732ax | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190412 | 206305 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2AY | SA732AY | sa73 2ay | sa732ay | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190434 | 206359 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BA | SA732BA | sa73 2ba | sa732ba | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190314 | 206290 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BB | SA732BB | sa73 2bb | sa732bb | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190320 | 206254 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BD | SA732BD | sa73 2bd | sa732bd | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190261 | 206197 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BE | SA732BE | sa73 2be | sa732be | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190265 | 206222 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BG | SA732BG | sa73 2bg | sa732bg | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190226 | 206183 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BH | SA732BH | sa73 2bh | sa732bh | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190267 | 206329 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BL | SA732BL | sa73 2bl | sa732bl | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190120 | 206287 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BN | SA732BN | sa73 2bn | sa732bn | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190221 | 206299 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BP | SA732BP | sa73 2bp | sa732bp | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190084 | 206286 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BR | SA732BR | sa73 2br | sa732br | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190596 | 206432 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BT | SA732BT | sa73 2bt | sa732bt | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190120 | 206128 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BU | SA732BU | sa73 2bu | sa732bu | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190099 | 206144 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BW | SA732BW | sa73 2bw | sa732bw | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190194 | 206292 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BX | SA732BX | sa73 2bx | sa732bx | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190140 | 206173 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BY | SA732BY | sa73 2by | sa732by | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190169 | 206117 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2BZ | SA732BZ | sa73 2bz | sa732bz | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190365 | 206389 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DA | SA732DA | sa73 2da | sa732da | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190603 | 207404 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DE | SA732DE | sa73 2de | sa732de | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190770 | 207488 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DF | SA732DF | sa73 2df | sa732df | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190562 | 205864 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DH | SA732DH | sa73 2dh | sa732dh | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190249 | 206065 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DJ | SA732DJ | sa73 2dj | sa732dj | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190268 | 206028 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DL | SA732DL | sa73 2dl | sa732dl | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190417 | 205985 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DP | SA732DP | sa73 2dp | sa732dp | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190472 | 206002 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DR | SA732DR | sa73 2dr | sa732dr | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190460 | 206013 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DS | SA732DS | sa73 2ds | sa732ds | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190373 | 206062 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DT | SA732DT | sa73 2dt | sa732dt | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190412 | 206095 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DX | SA732DX | sa73 2dx | sa732dx | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190423 | 206201 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DY | SA732DY | sa73 2dy | sa732dy | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190449 | 206200 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2DZ | SA732DZ | sa73 2dz | sa732dz | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190474 | 206251 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2EA | SA732EA | sa73 2ea | sa732ea | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190503 | 206378 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2EB | SA732EB | sa73 2eb | sa732eb | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190594 | 206737 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2ED | SA732ED | sa73 2ed | sa732ed | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190518 | 206345 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2EE | SA732EE | sa73 2ee | sa732ee | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190590 | 206517 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2EG | SA732EG | sa73 2eg | sa732eg | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190598 | 206849 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2EH | SA732EH | sa73 2eh | sa732eh | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190528 | 206961 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2EJ | SA732EJ | sa73 2ej | sa732ej | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190644 | 206945 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2EL | SA732EL | sa73 2el | sa732el | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190619 | 207016 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2EN | SA732EN | sa73 2en | sa732en | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190420 | 207089 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2EP | SA732EP | sa73 2ep | sa732ep | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190510 | 206485 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2EQ | SA732EQ | sa73 2eq | sa732eq | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190511 | 206912 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2ER | SA732ER | sa73 2er | sa732er | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190442 | 206992 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2ES | SA732ES | sa73 2es | sa732es | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190427 | 206939 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HA | SA732HA | sa73 2ha | sa732ha | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190435 | 205954 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HE | SA732HE | sa73 2he | sa732he | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190450 | 205923 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HH | SA732HH | sa73 2hh | sa732hh | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190491 | 205907 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HJ | SA732HJ | sa73 2hj | sa732hj | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190512 | 206012 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HL | SA732HL | sa73 2hl | sa732hl | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190521 | 205908 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HP | SA732HP | sa73 2hp | sa732hp | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190780 | 205872 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HR | SA732HR | sa73 2hr | sa732hr | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190786 | 205926 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HS | SA732HS | sa73 2hs | sa732hs | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190636 | 205965 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HT | SA732HT | sa73 2ht | sa732ht | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190663 | 205931 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HU | SA732HU | sa73 2hu | sa732hu | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190660 | 205965 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HW | SA732HW | sa73 2hw | sa732hw | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190647 | 205906 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HX | SA732HX | sa73 2hx | sa732hx | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190540 | 205962 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2HY | SA732HY | sa73 2hy | sa732hy | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190498 | 206113 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JA | SA732JA | sa73 2ja | sa732ja | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190579 | 206081 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JB | SA732JB | sa73 2jb | sa732jb | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190542 | 206175 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JD | SA732JD | sa73 2jd | sa732jd | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190594 | 206098 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JE | SA732JE | sa73 2je | sa732je | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190603 | 205882 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JF | SA732JF | sa73 2jf | sa732jf | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190697 | 205989 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JG | SA732JG | sa73 2jg | sa732jg | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190565 | 206189 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JH | SA732JH | sa73 2jh | sa732jh | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190748 | 206010 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JJ | SA732JJ | sa73 2jj | sa732jj | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190643 | 206094 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JL | SA732JL | sa73 2jl | sa732jl | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190667 | 206104 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JN | SA732JN | sa73 2jn | sa732jn | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190557 | 206245 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JP | SA732JP | sa73 2jp | sa732jp | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190685 | 206287 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JQ | SA732JQ | sa73 2jq | sa732jq | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190744 | 205905 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JR | SA732JR | sa73 2jr | sa732jr | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190600 | 206314 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JS | SA732JS | sa73 2js | sa732js | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190566 | 206379 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JT | SA732JT | sa73 2jt | sa732jt | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190635 | 206056 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2JW | SA732JW | sa73 2jw | sa732jw | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190478 | 206050 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LA | SA732LA | sa73 2la | sa732la | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190852 | 205797 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LB | SA732LB | sa73 2lb | sa732lb | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190944 | 205850 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LD | SA732LD | sa73 2ld | sa732ld | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191091 | 205831 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LE | SA732LE | sa73 2le | sa732le | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190877 | 205870 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LF | SA732LF | sa73 2lf | sa732lf | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191069 | 205901 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LG | SA732LG | sa73 2lg | sa732lg | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190887 | 205907 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LH | SA732LH | sa73 2lh | sa732lh | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190851 | 205930 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LJ | SA732LJ | sa73 2lj | sa732lj | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190880 | 205935 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LL | SA732LL | sa73 2ll | sa732ll | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190998 | 205936 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LN | SA732LN | sa73 2ln | sa732ln | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190870 | 206037 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LP | SA732LP | sa73 2lp | sa732lp | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190802 | 205955 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LQ | SA732LQ | sa73 2lq | sa732lq | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190728 | 206238 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LR | SA732LR | sa73 2lr | sa732lr | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190808 | 206017 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LS | SA732LS | sa73 2ls | sa732ls | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190741 | 206109 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LT | SA732LT | sa73 2lt | sa732lt | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190814 | 206071 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LU | SA732LU | sa73 2lu | sa732lu | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190907 | 206027 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LW | SA732LW | sa73 2lw | sa732lw | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190653 | 206189 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LX | SA732LX | sa73 2lx | sa732lx | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 191005 | 206049 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LY | SA732LY | sa73 2ly | sa732ly | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190989 | 206079 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2LZ | SA732LZ | sa73 2lz | sa732lz | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190910 | 205988 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NA | SA732NA | sa73 2na | sa732na | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190926 | 206165 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NB | SA732NB | sa73 2nb | sa732nb | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190828 | 206201 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2ND | SA732ND | sa73 2nd | sa732nd | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190939 | 206300 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NE | SA732NE | sa73 2ne | sa732ne | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190982 | 206352 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NJ | SA732NJ | sa73 2nj | sa732nj | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191189 | 205872 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NL | SA732NL | sa73 2nl | sa732nl | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191115 | 205920 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NN | SA732NN | sa73 2nn | sa732nn | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191158 | 205954 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NP | SA732NP | sa73 2np | sa732np | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191092 | 205982 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NR | SA732NR | sa73 2nr | sa732nr | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191065 | 206146 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NS | SA732NS | sa73 2ns | sa732ns | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 191016 | 206180 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NT | SA732NT | sa73 2nt | sa732nt | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191058 | 206305 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NU | SA732NU | sa73 2nu | sa732nu | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191296 | 206178 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NX | SA732NX | sa73 2nx | sa732nx | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191183 | 206030 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NY | SA732NY | sa73 2ny | sa732ny | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191232 | 206192 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2NZ | SA732NZ | sa73 2nz | sa732nz | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191071 | 206260 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PA | SA732PA | sa73 2pa | sa732pa | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191186 | 206163 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PB | SA732PB | sa73 2pb | sa732pb | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191116 | 206158 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PD | SA732PD | sa73 2pd | sa732pd | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190914 | 206377 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PE | SA732PE | sa73 2pe | sa732pe | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190784 | 206623 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PF | SA732PF | sa73 2pf | sa732pf | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190884 | 206734 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PG | SA732PG | sa73 2pg | sa732pg | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190975 | 206486 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PH | SA732PH | sa73 2ph | sa732ph | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190873 | 206623 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PJ | SA732PJ | sa73 2pj | sa732pj | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190702 | 206779 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PL | SA732PL | sa73 2pl | sa732pl | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190930 | 206501 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PN | SA732PN | sa73 2pn | sa732pn | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190814 | 206629 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PP | SA732PP | sa73 2pp | sa732pp | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190767 | 206918 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PQ | SA732PQ | sa73 2pq | sa732pq | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190957 | 206655 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PR | SA732PR | sa73 2pr | sa732pr | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190729 | 206632 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PS | SA732PS | sa73 2ps | sa732ps | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190786 | 206756 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PW | SA732PW | sa73 2pw | sa732pw | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190673 | 206737 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2PX | SA732PX | sa73 2px | sa732px | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190858 | 206343 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2QA | SA732QA | sa73 2qa | sa732qa | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190987 | 205639 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2QB | SA732QB | sa73 2qb | sa732qb | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191165 | 205712 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2QD | SA732QD | sa73 2qd | sa732qd | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191202 | 205620 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2QE | SA732QE | sa73 2qe | sa732qe | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191178 | 205590 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2QH | SA732QH | sa73 2qh | sa732qh | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191245 | 205614 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2QJ | SA732QJ | sa73 2qj | sa732qj | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191218 | 205668 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2QL | SA732QL | sa73 2ql | sa732ql | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191194 | 205782 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2QN | SA732QN | sa73 2qn | sa732qn | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191272 | 205711 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2QP | SA732QP | sa73 2qp | sa732qp | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191278 | 205858 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2QR | SA732QR | sa73 2qr | sa732qr | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191342 | 205815 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2QS | SA732QS | sa73 2qs | sa732qs | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191282 | 205760 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2QT | SA732QT | sa73 2qt | sa732qt | Pembrokeshire |  | Milford Haven |  | 1070 | 900-1200 | 2.1416 | 1.5671 | 1.1492 | 19.9431 | 10.6363 | 11.7559 | 191331 | 205960 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RA | SA732RA | sa73 2ra | sa732ra | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191506 | 207638 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RB | SA732RB | sa73 2rb | sa732rb | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191043 | 206556 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RD | SA732RD | sa73 2rd | sa732rd | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191069 | 206665 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RE | SA732RE | sa73 2re | sa732re | Pembrokeshire |  | Milford Haven |  | 1097 | 900-1200 | 2.1957 | 1.6066 | 1.1782 | 20.4464 | 10.9047 | 12.0526 | 190988 | 206837 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RF | SA732RF | sa73 2rf | sa732rf | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190933 | 207079 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RG | SA732RG | sa73 2rg | sa732rg | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191072 | 207021 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RH | SA732RH | sa73 2rh | sa732rh | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191069 | 206811 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RJ | SA732RJ | sa73 2rj | sa732rj | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191094 | 207133 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RL | SA732RL | sa73 2rl | sa732rl | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191163 | 206979 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RN | SA732RN | sa73 2rn | sa732rn | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191136 | 207052 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RP | SA732RP | sa73 2rp | sa732rp | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 191006 | 207302 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RQ | SA732RQ | sa73 2rq | sa732rq | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191035 | 207126 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RR | SA732RR | sa73 2rr | sa732rr | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190764 | 207416 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RS | SA732RS | sa73 2rs | sa732rs | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190836 | 207569 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RT | SA732RT | sa73 2rt | sa732rt | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190991 | 207497 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RU | SA732RU | sa73 2ru | sa732ru | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190933 | 207493 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RW | SA732RW | sa73 2rw | sa732rw | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190943 | 207104 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RX | SA732RX | sa73 2rx | sa732rx | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190698 | 207470 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RY | SA732RY | sa73 2ry | sa732ry | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190689 | 207209 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2RZ | SA732RZ | sa73 2rz | sa732rz | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190731 | 207435 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2SA | SA732SA | sa73 2sa | sa732sa | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191236 | 207464 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2SB | SA732SB | sa73 2sb | sa732sb | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191241 | 207433 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2SD | SA732SD | sa73 2sd | sa732sd | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191171 | 206909 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2SE | SA732SE | sa73 2se | sa732se | Pembrokeshire |  | Milford Haven |  | 1106 | 900-1200 | 2.2137 | 1.6198 | 1.1878 | 20.6141 | 10.9942 | 12.1515 | 191298 | 207529 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 2SH | SA732SH | sa73 2sh | sa732sh | Pembrokeshire |  | Milford Haven |  | 1091 | 900-1200 | 2.1837 | 1.5978 | 1.1717 | 20.3345 | 10.8451 | 11.9867 | 191139 | 206916 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3AA | SA733AA | sa73 3aa | sa733aa | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190217 | 205826 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3AB | SA733AB | sa73 3ab | sa733ab | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190065 | 205965 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3AH | SA733AH | sa73 3ah | sa733ah | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190144 | 205848 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3AJ | SA733AJ | sa73 3aj | sa733aj | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190292 | 205794 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3AL | SA733AL | sa73 3al | sa733al | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190304 | 205911 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3AQ | SA733AQ | sa73 3aq | sa733aq | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189881 | 205820 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3AU | SA733AU | sa73 3au | sa733au | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189931 | 206261 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3AW | SA733AW | sa73 3aw | sa733aw | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190251 | 205928 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3AX | SA733AX | sa73 3ax | sa733ax | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189837 | 205863 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3AY | SA733AY | sa73 3ay | sa733ay | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190349 | 205777 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3AZ | SA733AZ | sa73 3az | sa733az | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190413 | 205751 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3BA | SA733BA | sa73 3ba | sa733ba | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190679 | 205615 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3BB | SA733BB | sa73 3bb | sa733bb | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190647 | 205735 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3BD | SA733BD | sa73 3bd | sa733bd | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190575 | 205718 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3BH | SA733BH | sa73 3bh | sa733bh | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190192 | 205671 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3BN | SA733BN | sa73 3bn | sa733bn | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190250 | 205642 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3BP | SA733BP | sa73 3bp | sa733bp | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189631 | 205765 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3BR | SA733BR | sa73 3br | sa733br | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189176 | 206258 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3BT | SA733BT | sa73 3bt | sa733bt | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189662 | 205613 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3BU | SA733BU | sa73 3bu | sa733bu | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189741 | 205598 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3BX | SA733BX | sa73 3bx | sa733bx | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189799 | 205520 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3BY | SA733BY | sa73 3by | sa733by | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189948 | 205508 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DA | SA733DA | sa73 3da | sa733da | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189846 | 205447 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DB | SA733DB | sa73 3db | sa733db | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189955 | 205472 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DD | SA733DD | sa73 3dd | sa733dd | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189918 | 205528 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DE | SA733DE | sa73 3de | sa733de | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189997 | 205531 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DG | SA733DG | sa73 3dg | sa733dg | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190042 | 205470 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DJ | SA733DJ | sa73 3dj | sa733dj | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189842 | 205908 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DL | SA733DL | sa73 3dl | sa733dl | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189896 | 205613 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DN | SA733DN | sa73 3dn | sa733dn | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189828 | 205604 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DP | SA733DP | sa73 3dp | sa733dp | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189829 | 205689 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DR | SA733DR | sa73 3dr | sa733dr | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189827 | 205722 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DW | SA733DW | sa73 3dw | sa733dw | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189722 | 205738 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DY | SA733DY | sa73 3dy | sa733dy | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189470 | 205724 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3DZ | SA733DZ | sa73 3dz | sa733dz | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189568 | 205752 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EA | SA733EA | sa73 3ea | sa733ea | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189613 | 205617 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EB | SA733EB | sa73 3eb | sa733eb | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189569 | 205584 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3ED | SA733ED | sa73 3ed | sa733ed | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189523 | 205717 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EE | SA733EE | sa73 3ee | sa733ee | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189415 | 205672 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EF | SA733EF | sa73 3ef | sa733ef | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189469 | 205513 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EG | SA733EG | sa73 3eg | sa733eg | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189397 | 205606 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EH | SA733EH | sa73 3eh | sa733eh | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189532 | 205618 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EJ | SA733EJ | sa73 3ej | sa733ej | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189324 | 205663 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EL | SA733EL | sa73 3el | sa733el | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189290 | 205787 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EN | SA733EN | sa73 3en | sa733en | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189207 | 205785 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EP | SA733EP | sa73 3ep | sa733ep | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189232 | 205541 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EQ | SA733EQ | sa73 3eq | sa733eq | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189306 | 205611 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3ES | SA733ES | sa73 3es | sa733es | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189205 | 205856 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3ET | SA733ET | sa73 3et | sa733et | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189262 | 205919 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EU | SA733EU | sa73 3eu | sa733eu | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189341 | 205893 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EW | SA733EW | sa73 3ew | sa733ew | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189167 | 205665 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3EX | SA733EX | sa73 3ex | sa733ex | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189412 | 205838 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HB | SA733HB | sa73 3hb | sa733hb | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189163 | 205427 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HD | SA733HD | sa73 3hd | sa733hd | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188970 | 206233 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HE | SA733HE | sa73 3he | sa733he | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188873 | 206182 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HF | SA733HF | sa73 3hf | sa733hf | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188742 | 206194 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HG | SA733HG | sa73 3hg | sa733hg | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188873 | 206089 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HH | SA733HH | sa73 3hh | sa733hh | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188929 | 206122 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HJ | SA733HJ | sa73 3hj | sa733hj | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188707 | 206269 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HL | SA733HL | sa73 3hl | sa733hl | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188774 | 206097 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HN | SA733HN | sa73 3hn | sa733hn | Pembrokeshire |  | Milford Haven |  | 1071 | 900-1200 | 2.1436 | 1.5685 | 1.1502 | 19.9618 | 10.6463 | 11.7669 | 188891 | 205901 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HP | SA733HP | sa73 3hp | sa733hp | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188684 | 206283 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HQ | SA733HQ | sa73 3hq | sa733hq | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188825 | 206243 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HR | SA733HR | sa73 3hr | sa733hr | Pembrokeshire |  | Milford Haven |  | 1071 | 900-1200 | 2.1436 | 1.5685 | 1.1502 | 19.9618 | 10.6463 | 11.7669 | 188902 | 205874 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HS | SA733HS | sa73 3hs | sa733hs | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188852 | 206040 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HT | SA733HT | sa73 3ht | sa733ht | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188989 | 206023 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HU | SA733HU | sa73 3hu | sa733hu | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188904 | 205979 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HW | SA733HW | sa73 3hw | sa733hw | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188884 | 206297 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3HX | SA733HX | sa73 3hx | sa733hx | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188909 | 206078 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3JA | SA733JA | sa73 3ja | sa733ja | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190393 | 205886 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3JH | SA733JH | sa73 3jh | sa733jh | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190469 | 205820 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3JJ | SA733JJ | sa73 3jj | sa733jj | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190473 | 205868 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3JN | SA733JN | sa73 3jn | sa733jn | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190611 | 205849 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3JP | SA733JP | sa73 3jp | sa733jp | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190724 | 205803 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3JR | SA733JR | sa73 3jr | sa733jr | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190746 | 205689 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3JU | SA733JU | sa73 3ju | sa733ju | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190803 | 205715 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3JW | SA733JW | sa73 3jw | sa733jw | Pembrokeshire |  | Milford Haven |  | 1063 | 900-1200 | 2.1276 | 1.5568 | 1.1417 | 19.8127 | 10.5667 | 11.679 | 190769 | 205751 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LD | SA733LD | sa73 3ld | sa733ld | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189834 | 206270 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LE | SA733LE | sa73 3le | sa733le | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189899 | 206106 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LF | SA733LF | sa73 3lf | sa733lf | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189862 | 206171 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LG | SA733LG | sa73 3lg | sa733lg | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189887 | 206086 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LH | SA733LH | sa73 3lh | sa733lh | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189798 | 206037 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LJ | SA733LJ | sa73 3lj | sa733lj | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189778 | 205909 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LL | SA733LL | sa73 3ll | sa733ll | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189711 | 205866 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LN | SA733LN | sa73 3ln | sa733ln | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189728 | 205952 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LP | SA733LP | sa73 3lp | sa733lp | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189767 | 205831 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LQ | SA733LQ | sa73 3lq | sa733lq | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189785 | 205966 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LR | SA733LR | sa73 3lr | sa733lr | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189853 | 205778 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LS | SA733LS | sa73 3ls | sa733ls | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189840 | 206205 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LT | SA733LT | sa73 3lt | sa733lt | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189873 | 205799 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LU | SA733LU | sa73 3lu | sa733lu | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189676 | 205907 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LW | SA733LW | sa73 3lw | sa733lw | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189660 | 205970 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3LX | SA733LX | sa73 3lx | sa733lx | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189660 | 205886 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3NA | SA733NA | sa73 3na | sa733na | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189633 | 206020 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3NB | SA733NB | sa73 3nb | sa733nb | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189750 | 206101 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3ND | SA733ND | sa73 3nd | sa733nd | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189661 | 206104 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3NE | SA733NE | sa73 3ne | sa733ne | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189566 | 206186 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3NG | SA733NG | sa73 3ng | sa733ng | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189695 | 206165 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3NH | SA733NH | sa73 3nh | sa733nh | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189574 | 206277 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3NJ | SA733NJ | sa73 3nj | sa733nj | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189510 | 206440 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3NL | SA733NL | sa73 3nl | sa733nl | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189387 | 206395 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3NN | SA733NN | sa73 3nn | sa733nn | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189358 | 206445 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3NR | SA733NR | sa73 3nr | sa733nr | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189357 | 206523 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3NW | SA733NW | sa73 3nw | sa733nw | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189358 | 206482 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PA | SA733PA | sa73 3pa | sa733pa | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189654 | 205812 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PB | SA733PB | sa73 3pb | sa733pb | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189594 | 205864 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PD | SA733PD | sa73 3pd | sa733pd | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189531 | 206012 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PE | SA733PE | sa73 3pe | sa733pe | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189507 | 206111 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PF | SA733PF | sa73 3pf | sa733pf | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189417 | 206188 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PG | SA733PG | sa73 3pg | sa733pg | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189426 | 206273 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PH | SA733PH | sa73 3ph | sa733ph | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189309 | 206274 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PJ | SA733PJ | sa73 3pj | sa733pj | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189299 | 206324 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PL | SA733PL | sa73 3pl | sa733pl | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 189015 | 206290 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PP | SA733PP | sa73 3pp | sa733pp | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189068 | 205663 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PQ | SA733PQ | sa73 3pq | sa733pq | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189098 | 206477 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PR | SA733PR | sa73 3pr | sa733pr | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189043 | 206381 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PS | SA733PS | sa73 3ps | sa733ps | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189156 | 206322 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PT | SA733PT | sa73 3pt | sa733pt | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189142 | 206393 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PU | SA733PU | sa73 3pu | sa733pu | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189180 | 206489 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PW | SA733PW | sa73 3pw | sa733pw | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189200 | 206380 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PY | SA733PY | sa73 3py | sa733py | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189499 | 206886 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3PZ | SA733PZ | sa73 3pz | sa733pz | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189570 | 206888 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3QA | SA733QA | sa73 3qa | sa733qa | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189607 | 206804 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3QB | SA733QB | sa73 3qb | sa733qb | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189574 | 206122 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3QD | SA733QD | sa73 3qd | sa733qd | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189656 | 206823 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3QH | SA733QH | sa73 3qh | sa733qh | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189620 | 206405 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3QP | SA733QP | sa73 3qp | sa733qp | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189483 | 206027 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3QR | SA733QR | sa73 3qr | sa733qr | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189335 | 206009 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3QS | SA733QS | sa73 3qs | sa733qs | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189274 | 206035 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3QT | SA733QT | sa73 3qt | sa733qt | Pembrokeshire |  | Milford Haven |  | 1083 | 900-1200 | 2.1677 | 1.5861 | 1.1631 | 20.1854 | 10.7656 | 11.8988 | 189219 | 205972 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3QU | SA733QU | sa73 3qu | sa733qu | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189237 | 206123 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3QX | SA733QX | sa73 3qx | sa733qx | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189348 | 206098 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3QY | SA733QY | sa73 3qy | sa733qy | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189337 | 206181 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3QZ | SA733QZ | sa73 3qz | sa733qz | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189259 | 206209 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3RA | SA733RA | sa73 3ra | sa733ra | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189109 | 206131 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3RB | SA733RB | sa73 3rb | sa733rb | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189052 | 206070 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3RD | SA733RD | sa73 3rd | sa733rd | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189048 | 206184 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3RE | SA733RE | sa73 3re | sa733re | Pembrokeshire |  | Milford Haven |  | 1092 | 900-1200 | 2.1857 | 1.5993 | 1.1728 | 20.3532 | 10.855 | 11.9977 | 189023 | 206255 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3RG | SA733RG | sa73 3rg | sa733rg | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 189005 | 206318 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3RH | SA733RH | sa73 3rh | sa733rh | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 189002 | 206131 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3RJ | SA733RJ | sa73 3rj | sa733rj | Pembrokeshire |  | Milford Haven |  | 1071 | 900-1200 | 2.1436 | 1.5685 | 1.1502 | 19.9618 | 10.6463 | 11.7669 | 188863 | 205821 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3RL | SA733RL | sa73 3rl | sa733rl | Pembrokeshire |  | Milford Haven |  | 1071 | 900-1200 | 2.1436 | 1.5685 | 1.1502 | 19.9618 | 10.6463 | 11.7669 | 188899 | 205738 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3RQ | SA733RQ | sa73 3rq | sa733rq | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188966 | 206317 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3RS | SA733RS | sa73 3rs | sa733rs | Pembrokeshire |  | Milford Haven |  | 1071 | 900-1200 | 2.1436 | 1.5685 | 1.1502 | 19.9618 | 10.6463 | 11.7669 | 188493 | 205693 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3SA | SA733SA | sa73 3sa | sa733sa | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188694 | 206580 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3SB | SA733SB | sa73 3sb | sa733sb | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188672 | 206571 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3SD | SA733SD | sa73 3sd | sa733sd | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188771 | 206501 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3SE | SA733SE | sa73 3se | sa733se | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188711 | 206677 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3SF | SA733SF | sa73 3sf | sa733sf | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188629 | 206753 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3SG | SA733SG | sa73 3sg | sa733sg | Pembrokeshire |  | Milford Haven |  | 1108 | 900-1200 | 2.2177 | 1.6227 | 1.19 | 20.6514 | 11.0141 | 12.1734 | 188649 | 206548 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3SH | SA733SH | sa73 3sh | sa733sh | PCNPA |  | Herbrandston |  | 1119 | 900-1200 | 2.2397 | 1.6388 | 1.2018 | 20.8564 | 11.1234 | 12.2943 | 187098 | 207834 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 3SJ | SA733SJ | sa73 3sj | sa733sj | PCNPA |  | Herbrandston |  | 1119 | 900-1200 | 2.2397 | 1.6388 | 1.2018 | 20.8564 | 11.1234 | 12.2943 | 187029 | 207584 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 3SL | SA733SL | sa73 3sl | sa733sl | PCNPA |  | Herbrandston |  | 1109 | 900-1200 | 2.2197 | 1.6242 | 1.1911 | 20.67 | 11.024 | 12.1844 | 186910 | 207523 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 3SP | SA733SP | sa73 3sp | sa733sp | PCNPA |  | Herbrandston |  | 1109 | 900-1200 | 2.2197 | 1.6242 | 1.1911 | 20.67 | 11.024 | 12.1844 | 186868 | 207622 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 3SS | SA733SS | sa73 3ss | sa733ss | PCNPA |  | Herbrandston |  | 1109 | 900-1200 | 2.2197 | 1.6242 | 1.1911 | 20.67 | 11.024 | 12.1844 | 186995 | 207371 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 3SU | SA733SU | sa73 3su | sa733su | PCNPA |  | Herbrandston |  | 1103 | 900-1200 | 2.2077 | 1.6154 | 1.1846 | 20.5582 | 10.9644 | 12.1185 | 187059 | 206788 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 3TB | SA733TB | sa73 3tb | sa733tb | PCNPA |  | Herbrandston |  | 1109 | 900-1200 | 2.2197 | 1.6242 | 1.1911 | 20.67 | 11.024 | 12.1844 | 186968 | 207664 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 3TD | SA733TD | sa73 3td | sa733td | PCNPA |  | Herbrandston |  | 1109 | 900-1200 | 2.2197 | 1.6242 | 1.1911 | 20.67 | 11.024 | 12.1844 | 186907 | 207749 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 3TF | SA733TF | sa73 3tf | sa733tf | PCNPA |  | Herbrandston |  | 1109 | 900-1200 | 2.2197 | 1.6242 | 1.1911 | 20.67 | 11.024 | 12.1844 | 186988 | 207884 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 3TN | SA733TN | sa73 3tn | sa733tn | Pembrokeshire |  | Tiers Cross |  | 1188 | 900-1200 | 2.3778 | 1.7399 | 1.2759 | 22.1425 | 11.8093 | 13.0524 | 189829 | 210070 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3TP | SA733TP | sa73 3tp | sa733tp | PCNPA |  | Herbrandston |  | 1109 | 900-1200 | 2.2197 | 1.6242 | 1.1911 | 20.67 | 11.024 | 12.1844 | 187001 | 207759 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 3TS | SA733TS | sa73 3ts | sa733ts | PCNPA |  | Herbrandston |  | 1109 | 900-1200 | 2.2197 | 1.6242 | 1.1911 | 20.67 | 11.024 | 12.1844 | 186888 | 207856 | Pembrokeshire Coast National Park LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA73 3UA | SA733UA | sa73 3ua | sa733ua | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190322 | 207244 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3UB | SA733UB | sa73 3ub | sa733ub | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190239 | 207289 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3UD | SA733UD | sa73 3ud | sa733ud | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190395 | 207762 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3UE | SA733UE | sa73 3ue | sa733ue | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190364 | 207810 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3UF | SA733UF | sa73 3uf | sa733uf | Pembrokeshire |  | Milford Haven |  | 1086 | 900-1200 | 2.1737 | 1.5905 | 1.1664 | 20.2413 | 10.7954 | 11.9317 | 190199 | 207980 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3UG | SA733UG | sa73 3ug | sa733ug | Pembrokeshire |  | Milford Haven |  | 1066 | 900-1200 | 2.1336 | 1.5612 | 1.1449 | 19.8686 | 10.5966 | 11.712 | 190378 | 207922 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA73 3UP | SA733UP | sa73 3up | sa733up | Pembrokeshire |  | Milford Haven |  | 1086 | 900-1200 | 2.1737 | 1.5905 | 1.1664 | 20.2413 | 10.7954 | 11.9317 | 190200 | 208092 | Pembrokeshire LPA |  | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA8 4RX | SA84RX | sa8 4rx | sa84rx | Neath Port Talbot |  | Garnswllt |  | 1816 | Over1500 | 3.6348 | 2.6596 | 1.9504 | 33.8474 | 18.0519 | 19.9521 | 269466 | 208915 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA8 4SX | SA84SX | sa8 4sx | sa84sx | Neath Port Talbot | Castell-nedd Port Talbot | Garnswllt |  | 1808 | Over1500 | 3.6188 | 2.6479 | 1.9418 | 33.6983 | 17.9724 | 19.8643 | 270334 | 208836 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council
SA9 2RL | SA92RL | sa9 2rl | sa92rl | Neath Port Talbot |  | Garnswllt |  | 1951 | Over1500 | 3.905 | 2.8573 | 2.0954 | 36.3636 | 19.3939 | 21.4354 | 274462 | 211485 | Neath Port Talbot LPA |  | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council