## Instructions
Nutrient Budget Calculator for Special Areas of Conservation (SACs) in Wales
This calculator was created by Ricardo Energy and Environment and Arup for Welsh Government.
This is the English version of the calculator. This calculator is also available in Welsh/Cymraeg.
This calculator contains 6 worksheets with 11 tables in total.
This is the instructions cover sheet. It tells you how to use the calculator and gives an overview of each worksheet.
You can move between worksheets using the tabs at the bottom of the page.
If you use screen reading software, you can use 'Ctrl' + 'Page Down' keys to move between the tabs.
If you use a keyboard only, to open any link in this cover sheet first select the cell with the link and then press the 'Shift' + 'F10' keys or the 'Fn' + the 'Menu' keys, then press the letter 'O' twice to highlight 'Open Hyperlink' and press 'Enter'.
If you use a keyboard only, access dropdown lists by clicking the dropdown arrow or pressing the 'Alt' + 'Down' keys when the cell is selected.
Table of Contents
Topic of each worksheet | Link to each worksheet
Stage 1: additional nutrient loading from wastewater | Stage 1: additional nutrient loading from wastewater
Stage 2: nutrient loading from pre-existing landcovers | Stage 2: nutrient loading from pre-existing landcovers
Stage 3: nutrient loading from new landcovers | Stage 3: nutrient loading from new landcovers
Stage 3S: nutrient load removed through sustainable urban drainage systems (SuDS) | Stage 3S: nutrient load removed through SuDS
Stage 4: final nutrient budget calculation | Stage 4: final nutrient budget calculation
General information about the calculator
This calculator helps you calculate a nutrient budget for a new development within one of the nine Special Areas of Conservation (SACs) within Wales.
The development categories include: residential; commercial; tourism; leisure and public service infrastructure. The planning permission use classes have been categorised into each development category. These can be found in the guidance that accompanies this calculator.
The nutrient budget for a site is calculated in 4 key stages with an additional optional stage in which information about the SuDS features on the site can be entered. Each stage is implemented in worksheets 2 to 6 of this calculator.
The instructions for completing each stage of the nutrient budget methodology are shown in cell A2 of each worksheet. Additional instructions may also be in cell A3.
Each worksheet is connected through a set of formulas which calculate the final nutrient budget. The formulas use a set of lookup tables to find relevant values to determine the nutrient loading at each stage.
Before a nutrient budget can be completed using the methodology, certain site-specific details for the development site need to be determined and entered into Stage 1, Stage 2, Stage 3, and Stage 3S (if applicable).
The total phosphorus (TP) budget and total nitrogen (TN) generated is calculated automatically once all required inputs have been entered into Stage 1, Stage 2, Stage 3, and Stage 3S (if applicable). The calculation involves adding the values from Stage 1 and the result of Stage 3 subtract Stage 3S (if applicable), and then subtracting the values from the Stage 2. A 20% precautionary buffer is then added to the result. This calculation is completed automatically in the Stage 4 worksheet. This equation can be summarised as: (Stage 1 - Stage 2 + (Stage 3 - Stage 3S)) * 1.2 = Stage 4
The pre-populated values in this calculator have been identified through extensive research and modelling. The values are based on the best available evidence and are suitably precautionary to account for any uncertainty. This nutrient budget calculator can be used as supporting evidence for a Habitat Regulations Assessment (HRA). Specifically, this calculator can be used within an appropriate assessment to assess the likely significant effects of a proposal on the integrity of the site and its conservation objectives. It is highly unadvisable to edit the values in this tool without a sufficient evidence base to justify any changes.
When using this tool, it is recommended that you save a new copy of this workbook for each nutrient budget calculation, in order to retain a default blank copy. It may also be useful to open two calculators with one showing the instructions and one showing the calculator.
Notes on Stage 1: additional nutrient loading from wastewater
The Stage 1 Worksheet contains 2 tables that are used to calculate the nutrient load associated with the additional wastewater generated as a result of the development.
The first table under the heading 'Wastewater load input data' requires you to enter key information about the development and the water infrastructure. This table contains a mix of user inputs and values that are calculated automatically depending on the user inputs.
The first table contains a postcode search function that allows you to find the appropriate LPA and the rainfall for the site if a valid postcode is entered that is within the SAC catchment. Entering the postcode for the site, or the nearest postcode, will generate site specific information. This automatically generated information can be used instead of manually entering the relevant data. However it is your responsibility to confirm this information is correct.
The amount of wastewater generated needs to be calculated using the following: - the SAC relevant to the development - project type (residential, commercial, tourism, public service infrastructure or leisure) - number of additional dwellings/units being created - the local planning authority (LPA) - an average occupancy rate (if applicable) - number of people/customers/employees per unit - a per capita water usage figure per person/customer/employee - the number of customers/users & employees (if applicable) - the percentage of customers/users & employees from outside the catchment (if applicable) - the water usage per customer/user (if applicable)
You must select the Special Area of Conservation (SAC) for the calculator to function correctly.
You must select the project type because it determines which inputs are required to calculate the amount of wastewater generated. The project types are representative of the planning permission uses classes. The appropriate project type for each planning permission use class can be found in the guidance that accompanies this calculator.
The average occupancy rate for residential developments is dependent on the postcode entered or the LPA selected. The default water usage values is preset in the worksheet. The default setting for the average occupancy rate is preset in the worksheet and automatically generated dependant on the LPA. You can change this value if there is sufficient evidence that the development will be different to the national average. The per capita water usage is also present in the worksheet, this value should remain unchanged unless other efficiency measures are used. The number of new developments is not preset and must be a whole number.
You must select the wastewater treatment works (WwTW) that will receive the wastewater from the development. If you are unsure which WwTW will receive the wastewater, please obtain this information from Dwr Cymru/Welsh Water in order to complete this calculator. If connecting to a sewerage network is unfeasible and a septic tank or package treatment plant is being used, please select the appropriate option.
The WwTW are correct at the time of publication but may be subject to change in the future. If required, these values will be updated at a later date accordingly.
If you are using a septic tank or package treatment plant and the total nitrogen (TN) or total phosphorus (TP) final effluent concentrations are specified by the manufacturer, select 'Septic Tank user defined' or 'Package Treatment Plant user defined' and enter the manufacturer specified value in the cell where prompted (in mg/l).
The second table under the heading 'Final calculation of nutrient load from wastewater' contains the calculation of the nutrient load from additional wastewater generated by the development.
Notes on Stage 2: nutrient loading from pre-existing landcovers
The Stage 2 Worksheet contains 2 tables that are used for calculating the annual nutrient load from existing (pre-development) landcovers within the redline boundary of the development.
The first table under the heading 'Physical characteristics' requires user inputs. You must select the predominant soil drainage present within the redline boundary of the site. The rainfall value will be automatically generated if the user has entered a valid postcode in 'Stage 1'. You must select whether the rainfall value is correct. If the rainfall value is not correct, or if a valid postcode has not been entered, you must select the rainfall value from the dropdown list. The sources of the soil drainage type and the rainfall can be found in the table under the heading 'Sources of information required for Stage 2' that follows this text.
The second table under the heading 'Pre-existing landcovers' requires user inputs. You must select the most appropriate landcovers from a dropdown list of 18 landcover types to represent the landcover present on the site before the development. You must also enter the area of each landcover in hectares. The dropdown list contains 10 agricultural landcover types and 8 non-agricultural landcover types to represent the landcovers present on the site before development. The descriptions of each landcover type can be found in the guidance that accompanies this calculator. You must determine which landcover types are present within the redline boundary of the development before completing this tool. If there is a landcover within the development area that is not in the dropdown list please select the most similar landcover type.
Sources of information required for Stage 2
Description of information | Link to source of information
Soil drainage: The drainage associated with the predominant soil type within the development site can be found using the Soilscapes Map. | Soilscapes
Rainfall: The annual average rainfall that the development will receive can be found using the National River Flow Archive. You must first select any flow gauging station. You must navigate to the 'Catchment info' tab and select the spatial data type to view as 'Rainfall'. You can scroll around this map to find your development. Clicking the link will take the user to the 'Usk at Chainbridge' station. | National River Flow Archive (Usk at Chainbridge)
Notes on Stage 3: nutrient loading from new landcovers
The Stage 3 Worksheet contains one table which is used to calculate the annual nutrient load from new (post-development) landcovers within the redline boundary of the development. The type(s) and area(s) of landcover present on the new development is required to generate nutrient loads associated with the current landcovers on the site.
The second table under the heading 'New landcovers' requires user inputs. You must select the most appropriate landcovers from a dropdown list of 18 landcover types to represent the landcover present on the site following the development. You must also enter the area of each landcover in hectares. The dropdown list contains 10 agricultural landcover types and 8 non-agricultural landcover types to represent the landcovers present on the site before development. The descriptions of each landcover type can be found in the guidance that accompanies this calculator. You must determine which landcover types are present within the redline boundary of the development before completing this tool. If there is a landcover within the development area that is not in the dropdown list please select the most similar landcover type.
Notes on Stage 3S: nutrient load removed through SuDS
The Stage 3S Worksheet contains one table in which you can enter key information about the use of SuDS to treat the runoff from the site and reduce the nutrient loading from new landcovers.
In this section the user will need to enter information about the SuDS features used to calculate the amount of nutrients removed through SuDS treatment of surface runoff. This section must only be completed if SuDS are compliant with the national standards and are being implemented under the requirement of the Flood and Water Management Act 2010 (Schedule 3). Any SuDS that are being implemented in addition to the site plans for the purposes of mitigation must not be considered in the nutrient budget calculation for the site. In this instance, it is instead recommended that a second calculation is populated - the People over Wind judgment means that it is no longer possible to apply mitigation measures at the screening stage.
The landcovers and areas present on the new site will be automatically populated from Stage 3.
You will need to: - enter the catchment area that drains to the SuDS as a proportion of the new landcovers - choose the SuDS features used - enter the nutrient removal rates as a percentage
It is recommended that the surface area of the SuDS features are included within the area of the landcover that they drain. If required, you can split the landcover up in Stage 3 to demonstrate multiple drainage configurations. You can select a SuDS feature from a list of 23 options. If a SuDS management train that comprises multiple SuDS features is being implemented you should select the appropriate option from the start of the list. Otherwise, you should select the individual SuDS feature being used. If the appropriate SuDS feature cannot be found in the list, select the most relevant alternative. The nutrient removal rates should be entered as a whole number percentage between 0-100. You must be able to provide evidence for the removal rates you have entered. This is likely to require the submission of a drainage assessment and a detailed design of the SuDS features.
The amount of nutrients removed through SuDS is automatically calculated using the landcovers and associated loads from Stage 3, the drainage area, and the nutrient removal rates. The total load removed through SuDS is incorporated into the final nutrient budget calculation. Selecting the type of SuDS feature used is to ensure that the nutrient budget calculator matches the SuDS design detailed in the planning application.
Further information on SuDS can be found in the table under the heading 'Sources of information on SuDS and how to design them for nutrient removal' that follows this text.
Sources of information on SuDS and how to design them for nutrient removal
Description of information | Link to source of information
National standards for sustainable drainage systems (SuDS) can be found here: | National standards for sustainable drainage systems (SuDS)
Ciria's Using SuDS to reduce nitrogen in surface water runoff (C815) can be found here: | Using SuDS to reduce nitrogen in surface water runoff (C815)
Ciria's Using SuDS to reduce phosphorus in surface water runoff (C808F) can be found here: | Using SuDS to reduce phosphorus in surface water runoff (C808F)
Notes about the final annual nutrient budget
The Stage 4 Worksheet contains 2 tables which calculate the TP budget and the amount of TN generated.
The final stage automatically calculates the final nutrient budget using the results from Stage 1 to Stage 3S using the following equation: (Stage 1 - Stage 2 + (Stage 3 - Stage 3S)) * 1.2 = Stage 4
The first table under the heading 'Total phosphorus budget' calculates the amount of TP that you need to mitigate.
The second table under the heading 'Total nitrogen generated' calculates the amount of TN generated.
2026-02-09
v4

## Stage 1
Stage 1 - additional nutrient loading from wastewater
This sheet contains 2 tables. The tables are separated by a heading, which describes the following table. The first table labelled 'Wastewater load input data' requires user inputs. Cells A8, A9, A13, A17 to A20, A22 to A23 are automatically generated and will state 'Not applicable' unless the required user inputs have been entered. You will need to fill in cells B6, B7, B10 to B12 and B14 to B23, unless the description states 'Not applicable'. Cells B8, B9, B13 are automatically generated and will state 'Not applicable' unless the user inputs have been entered. If the user does not enter a postcode in cell B7, cells A9 and B9 will state 'Not applicable', however this data can be selected in Cell B6 in Stage 2. Cells B24 and B25 are automatically generated and will state '0.00' unless the user inputs have been entered. The second table labelled 'Final calculation of nutrient load from wastewater' does not require any user inputs. Cells B28 to B31 are automatically generated and will state '0.00' unless the user inputs have been entered in the second table labelled 'Wastewater load calculation table'.
How to fill in the table 'Wastewater load calculation table': Cell B6: Select the Special Area of Conservation (SAC) from the dropdown list. Cell B7: Enter the postcode, or the nearest postcode, for the proposed development site. This input is optional. Cell B10: Select the project type or development type from the dropdown list. Cell B11: Enter the number of additional units being created. Cell B12: Enter the Local Planning Authority the development is within, if a valid postcode has not been entered into cell B7. Cell B14: Select 'Yes' if the default occupancy rate is being used for the development if the project type is residential from the dropdown list. Select 'No' if the default occupancy rate does not apply to the residential development. Cell B15: Enter the average occupancy rate of the development if the default occupancy rate is not automatically generated in cell B13. Cell B16: Enter the water usage per resident or customer/user in litres per person per day. This value should be kept at 120 for residents unless other efficiency measures are used. Cell B17: Enter the percentage of customers/users coming from outside the catchment if the project type is not residential. The default value is set to 100%. Cell B18: Enter the number of employees per unit if the project type is not residential. Cell B19: Enter the water usage per resident or customer/user in litres per person per day. The default value is 120. Cell B20: Enter the percentage of employees coming from outside the catchment if the project type is not residential. The default value is set to 100%. Cell B21: Select the connecting wastewater treatment works (WwTW) from the dropdown list. Cell B22: Enter the certified value of total phosphorus (TP) if you select 'Package Treatment Plant user defined' or 'Septic Tank user defined' in cell B21. Otherwise the default values for these sewarage systems will be used in the calculation of the nutrient load associated with wastewater. Cell B23: Enter the certified value of total nitrogen (TN) if you select 'Package Treatment Plant user defined' or 'Septic Tank user defined' in cell B21. Otherwise the default values for these sewerage systems will be used in the calculation of the nutrient load associated with wastewater.
Wastewater load input data
Description of required information | Data entry column - user inputs required
Special Area of Conservation (SAC): | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid
Postcode: | LL13 7HP
Local Planning Authority (LPA): | Wrexham County Borough Council
Rainfall: | 791
Project type: | Residential
Development proposal (number of additional units): | 3
Not applicable | Not applicable
Default occupancy rate: | 2.33
Is this default value being used? | Yes
Not applicable
Water usage per resident (litres/person/day): | 120
Not applicable
Not applicable
Not applicable
Not applicable
Wastewater treatment works: | Five Fords STW
Not applicable
Not applicable
Phosphorus permitted limit (mg TP/l): | 1
Nitrogen permitted limit (mg TN/l): | 27
Final calculation of nutrient load from wastewater
Description of values generated | Values generated
Additional population: | 6.99
Annual wastewater production (litres): | 306371.7
Annual phosphorus load (kg TP/year): | 0.31
Annual nitrogen load (kg TN/year): | 8.27

## Stage 2
Stage 2 - nutrient loading from pre-existing landcovers
This sheet contains 2 tables. The tables are separated by a heading, which describes the following table. The first table labelled 'Physical characteristics' requires user inputs. You will need to fill in cells B5, B7 and B8 unless the description states 'Not applicable'. Cell B6 is automatically generated and will state 'Not applicable' unless a valid postcode has been entered into the previous worksheet. The second table labelled 'Pre-exisiting landcovers' requires user inputs. You will need to fill in cells A11 to B25. Cells B26 and C11 to D26 are automatically generated and will state '0.00' unless the required user inputs have been entered. Row 26 automatically calculates the 'Total' sum of cells B11 to B25 in cell B26, C11 to C25 in C26, and D11 to D25 in D26. How to fill in the table 'Physical characteristics': Cell B5: Select the appropriate soil drainage for the site from the dropdown list. Cell B7: Select 'Yes' if the automatically populated rainfall value is correct for the site if a valid postcode has been entered into the worksheet titled 'Stage 1'. Select 'No' if the automatically populated rainfall value is incorrect if a valid postcode has been entered into the worksheet titled 'Stage 1'. Cell B8: Select the annual average rainfall the development will receive from the dropdown list if a valid postcode has not been entered into the worksheet titled 'Stage 1'. How to fill in the table 'Pre-existing landcovers': Cells A11 to A25: Select the current (pre-development) land covers present within the redline boundary of the site. Cells B11 to B25: Enter the area in hectares of each land cover.
Physical characteristics
Description of required information | Data entry column - user inputs required
Soil drainage: | Impeded drainage
Rainfall identified using postcode (mm/year): | 791
Is this rainfall value correct? | Yes
Not applicable | Not applicable
Pre-existing landcovers
Landcover | Area (hectares) | Phosphorus load (kg TP/year) | Nitrogen load (kg TN/year)
Commercial/industrial land | 0.01 | 0.01 | 0.08
|  | 0 | 0
|  | 0 | 0
|  | 0 | 0
|  | 0 | 0
|  | 0 | 0
|  | 0 | 0
|  | 0 | 0
|  | 0 | 0
|  | 0 | 0
|  | 0 | 0
|  | 0 | 0
|  | 0 | 0
|  | 0 | 0
|  | 0 | 0
Total: | 0.01 | 0.01 | 0.08

## Stage 3
Stage 3 - nutrient loading from new landcovers
This sheet contains one table. A heading describes the table. The table is labelled 'New landcovers'. You will need to fill in cells A5 to B19. Cells B20, C5 to D19 are automatically generated and will state '0.00' unless the required user inputs have been entered. Cells E5 to E19 are automatically populated and will state 'Not applicable' unless the total area of the landcovers does not match the total area of the landcovers in the worksheet titled 'Stage 2'. Row 20 automatically calculates the 'Total' sum of cells B5 to B19 in cell B20, C5 to C19 in C20, and D5 to D19 in D20. How to fill in the table 'New landcovers': Cells A5 to A19: Choose the new (post-development) land covers present within the redline boundary of the site. Cells B5 to B19: Enter the area in hectares of each land cover.
New landcovers
Landcover | Area (hectares) | Phosphorus load (kg TP/year) | Nitrogen load (kg TN/year) | Notes on data
Residential land | 0.01 | 0.02 | 0.15 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
|  | 0 | 0 | Not applicable
Total: | 0.01 | 0.02 | 0.15 | Not applicable

## Stage 3S
Stage 3S - nutrient load removed through SuDS
This sheet contains one table. A heading describes the table. The table is labelled 'SuDS information'. SuDS stands for sustainable urban drainage systems. Cells A5 to A19 are automatically populated with landcovers entered into the worksheet titled 'Stage 3' and will state 'Not applicable' if landcovers have not been entered into the corresponding cells in the worksheet titled 'Stage 3'. Cells B5 to B20 are automatically populated with the area in hectares of the landcovers entered into the worksheet titled 'Stage 3' and will state '0.00' if areas have not been entered into the worksheet titled 'Stage 3'. You will need to fill in cells C5 to F19. Cells G5 to H20 are automatically calculated and will state '0.00' unless the required inputs have been entered. Row 20 automatically calculates the 'Total' sum of cells B5 to B19 in cell B20, the sum of cells G5 to G19 in cell G20 and the sum of cells H5 to H19 in cell H20. How to fill in the table 'SuDS information': Cells C5 to C19: Enter the size of the catchment area that drains to the SuDS feature as a proportion (%) of the landcover in the areas (in hectares). Cells D5 to D19: Select the SuDS feature that is being used to treat the run off from the dropdown list. Cells E5 to E19: Enter the phosphorus removal rate of the nutrient inputs as a percentage (%). Cells F5 to F19: Enter the nitrogen removal rate of the nutrient inputs as a percentage (%).
SuDS information
Landcover | Area (hectares) | Proportion of landcover area served by SuDS feature (%) | SuDS feature | P removal rate for SuDS feature | N removal rate for SuDS feature | Phosphorus load removed through SuDS (kg TP/year) | Nitrogen load removed through SuDS (kg TN/year)
Residential land | 0.01 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Not applicable | 0 |  |  |  |  | 0 | 0
Total: | 0.01 | Not applicable | Not applicable | Not applicable | Not applicable | 0 | 0 | P (%) | N (%)

## Stage 4
Stage 4 - final nutrient budget calculation
This sheet contains 2 tables. The tables are separated by a heading, which describes the following table. The tables are automatically calculated using the outputs from the previous stages. The first table labelled 'Total phosphorus budget' presents the calculations that underpin the final total phosphorus (TP) budget in cell B10. The second table labelled 'Total nitrogen generated' presents the calculations that underpin the final total nitrogen (TN) budget in cell B18. You do not need to fill in any cells in the tables. Cells B5 to B10 and B13 to B18 are automatically calculated. Cells B5 to B9 and cells B13 to B17 will state '0.00' unless user inputs have been entered to all of the required stages. Cell B10 will state 'No TP mitigation needed' if the phosphorus budget is less than 0.00 kilograms TP per year. Cell B18 will state 'No additional TN generated' if the nitrogen budget is less than 0.00 kilograms TN per year.
Total phosphorus budget
Description of phosphorus values generated | Values generated
Stage 1 phosphorus load (kg TP/year): | 0.31
Stage 2 phosphorus reduction (kg TP/year): | 0.01
Stage 3 phosphorus load (kg TP/year): | 0.02
Stage 3S phosphorus load removed through SuDS (kg TP/year): | 0
Phosphorus budget ((Stage 1 - Stage 2) + (Stage 3 - Stage 3S)): | 0.32
Phosphorus budget + 20% buffer | 0.38 kg TP/year requires mitigation
Total nitrogen generated
Description of nitrogen values generated | Values generated
Stage 1 nitrogen load (kg TN/year): | 8.27
Stage 2 nitrogen reduction (kg TN/year): | 0.08
Stage 3 nitrogen load (kg TN/year): | 0.15
Stage 3S nitrogen load removed through SuDS (TN kg/year): | 0
Nitrogen budget ((Stage 1 - Stage 2) + (Stage 3 - Stage 3S)): | 8.34
Nitrogen budget + 20% buffer: | 10.01 kg TN/year will be generated
Calculator version 4.0 - February 2026

## Lookups (hidden)
Lookup tables | Table 3: Permit levels last updated - | Table 3: light green = matches NRW permit list | [7 empty] | Table 3: light green = matches NRW permit list |  | Table 3: light green = matches NRW permit list
Table 1: SAC lookup | 2025-05-28 | Table 3: dark green = amended due to reaching permit change date | [7 empty] | Table 3: dark green = amended due to reaching permit change date |  | Table 3: dark green = amended due to reaching permit change date
SAC name | SAC link | [8 empty] | Table 3: light purple = amended to 8mg/l default as review period not started
Afon Eden - Cors Goch Trawsfynydd | https://sac.jncc.gov.uk/site/UK0030075 | [8 empty] | Table 3: red = amended to 8mg/l default as not covered by review
Afon Gwyrfai a Llyn Cwellyn | https://sac.jncc.gov.uk/site/UK0030046
Afon Teifi/ River Teifi | https://sac.jncc.gov.uk/site/UK0012670
Afon Tywi/ River Tywi | https://sac.jncc.gov.uk/site/UK0013010
Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | https://sac.jncc.gov.uk/site/UK0030074 - https://sac.jncc.gov.uk/site/UK0013116
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | https://sac.jncc.gov.uk/site/UK0020020
Bae Cemlyn/ Cemlyn Bay DIM AR GAEL/ NOT AVAILABLE | https://sac.jncc.gov.uk/site/UK0030114
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | https://sac.jncc.gov.uk/site/UK0014789
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | https://sac.jncc.gov.uk/site/UK0030252
River Usk/ Afon Wysg | https://sac.jncc.gov.uk/site/UK0013007
River Wye/ Afon Gwy | https://sac.jncc.gov.uk/site/UK0012642
Table 2: Stage 1 Local Planning Authority average occupancy rate
SAC | Awdurdodau cynllunio lleol | Local Planning Authority | Occupancy rate | Dynamic dropdown for LPA
Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | 2.3 | Conwy County Borough Council
Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council | 2.3 | Denbighshire County Council
Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park | 2.3 | Eryri National Park
Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council | 2.3 | Flintshire County Council
Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council | 2.31 | Gwynedd Council
Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council | 2.22 | Powys County Council
Afon Teifi/ River Teifi | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park | 2.22 | Wrexham County Borough Council
Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park | 2.21
Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council | 2.3
Afon Tywi/ River Tywi | Cyngor Sir Ceredigion | Ceredigion County Council | 2.31
Afon Tywi/ River Tywi | Cyngor Sir Powys | Powys County Council | 2.21
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council | 2.3
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot | Neath Port Talbot County Borough Council | 2.28
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cyngor Abertawe | Swansea Council | 2.27
Bae Cemlyn/ Cemlyn Bay | Cyngor Sir Yns Mon | Isle of Anglesey County Council | 2.24
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council | 2.3
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park | 2.3
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Conwy | Conwy County Borough Council | 2.2
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council | 2.33
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Gwynedd | Gwynedd Council | 2.3
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council | 2.26
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Powys | Powys County Council | 2.21
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council | 2.32
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Parc Cenedlaethol Eryri | Eryri National Park | 2.3
River Usk/ Afon Wysg | Cyngor Sir Powys | Powys County Council | 2.21
River Usk/ Afon Wysg | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park | 2.21
River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Caerffili | Caerphilly County Borough Council | 2.31
River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Blaenau Gwent | Blaenau Gwent County Borough Council | 2.21
River Usk/ Afon Wysg | Cyngor Bwrdeistref Sirol Torfaen | Torfaen County Borough Council | 2.3
River Usk/ Afon Wysg | Cyngor Sir Fynwy | Monmouthshire County Council | 2.27
River Usk/ Afon Wysg | Cyngor Dinas Casnewydd | Newport City Council | 2.41
River Wye/ Afon Gwy | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park | 2.21
River Wye/ Afon Gwy | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council | 2.3
River Wye/ Afon Gwy | Cyngor Sir Ceredigion | Ceredigion County Council | 2.31
River Wye/ Afon Gwy | Cyngor Sir Fynwy | Monmouthshire County Council | 2.27
River Wye/ Afon Gwy | Cyngor Sir Powys | Powys County Council | 2.21
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council | 2.3
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council | 2.22
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park | 2.22
Table 3: Wastewater Treatment Works Lookup table
SAC | site_name | Name_Final | permit_number | DWF | Daily_Flow | Local Authority | Watercourse | X coordinate | Y coordinate | Phosphorus permit pre DCWW upgrade | Phosphorus permit post DCWW upgrade | Nitrogen permit pre DCWW upgrade | Nitrogen permit post DCWW upgrade | Translation | Dynamic dropdown for LPA
Afon Eden - Cors Goch Trawsfynydd | BRONABER STW | Bronaber STW | CG0086701 | 141 |  | Gwynedd | AFON EDEN | 270400 | 331390 | 5 | 0.8 | 27 | 27 | Bronaber STW | Abenbury WwTW
Afon Eden - Cors Goch Trawsfynydd | GANLLWYD STW | Ganllwyd STW | CG0029001 |  |  | Gwynedd | MAWDDACH | 272800 | 324110 | 8 | 8 | 27 | 27 | Ganllwyd STW | Alwen Septic Tank
Afon Eden - Cors Goch Trawsfynydd | LLANFACHRETH WWTW | Llanfachreth WwTW | CG0110901 | 32.8 |  | Gwynedd | AFON Y LLAN | 275373 | 322343 | 5 | 5 | 27 | 27 | Llanfachreth WwTW | Bala WwTW
Afon Eden - Cors Goch Trawsfynydd | Package treatment plant (PTP) default | Package treatment plant (PTP) default | [7 empty] | 9.7 | 9.7 | 72.9 | 72.9 | Offer trin pecyn (PTP) rhagosodedig | Bangor On Dee STW
Afon Eden - Cors Goch Trawsfynydd | Package treatment plant (PTP) user defined | Package treatment plant (PTP) user defined | [11 empty] | Defnyddiwr offer trin pecyn (PTP) wedi'i ddiffinio | Betws Gwerfil Goch STW
Afon Eden - Cors Goch Trawsfynydd | Septic tank default | Septic tank default | [7 empty] | 11.6 | 11.6 | 96.3 | 96.3 | Tanc septig rhagosodedig | Bowling Bank STW
Afon Eden - Cors Goch Trawsfynydd | Septic tank user defined | Septic tank user defined | [11 empty] | Defnyddiwr tanc septig wedi'i ddiffinio | Bronington STW
Afon Gwyrfai a Llyn Cwellyn | BETWS GARMON WTW | Betws Garmon WwTW | CG0325001 | 8.4 |  | Gwynedd | AFON GWYRFAI | 254290 | 356740 | 8 | 8 | 27 | 27 | Betws Garmon WwTW | Bryneglwys STW
Afon Gwyrfai a Llyn Cwellyn | LLANFAGLAN WWTW FINAL EFFLUENT | Llanfaglan WwTW | CG0078101 | 1305.5 |  | Gwynedd | GWYRFAI | 246626 | 359370 | 1 | 0.7 | 27 | 27 | Llanfaglan WwTW | Carrog WwTW
Afon Gwyrfai a Llyn Cwellyn | Package treatment plant (PTP) default | Package treatment plant (PTP) default | [7 empty] | 9.7 | 9.7 | 72.9 | 72.9 | Offer trin pecyn (PTP) rhagosodedig | Cefn Brith STW
Afon Gwyrfai a Llyn Cwellyn | Package treatment plant (PTP) user defined | Package treatment plant (PTP) user defined | [11 empty] | Defnyddiwr offer trin pecyn (PTP) wedi'i ddiffinio | Cefn Mawr WwTW
Afon Gwyrfai a Llyn Cwellyn | RHYD DDU STW | Rhyd Ddu STW | CG0024101 |  |  | Gwynedd | GWYRFAI | 257050 | 353080 | 5 | 5 | 27 | 27 | Rhyd Ddu STW | Cerrigydrudion STW
Afon Gwyrfai a Llyn Cwellyn | Septic tank default | Septic tank default | [7 empty] | 11.6 | 11.6 | 96.3 | 96.3 | Tanc septig rhagosodedig | Cilcain Pantymwyn STW
Afon Gwyrfai a Llyn Cwellyn | Septic tank user defined | Septic tank user defined | [11 empty] | Defnyddiwr tanc septig wedi'i ddiffinio | Connahs Quay STW
Afon Gwyrfai a Llyn Cwellyn | WAUNFAWR STW (FINAL EFFLUENT) | Waunfawr STW | CG0134001 | 387 | 1242 | Gwynedd | AFON GWYRFAI | 252872 | 358980 | 5 | 1.6 | 27 | 27 | Waunfawr STW | Corwen WwTW
Afon Teifi/ River Teifi | Abercych Wastewater Treatment Works | Abercych WwTW | BG0034501 | 34.4 |  | Pembrokeshire | Nant Morw | 224348 | 241208 | 5 | 5 | 27 | 27 | Abercych WwTW | Cynwyd STW
Afon Teifi/ River Teifi | ADPAR WWTW ADPAR CEREDIGION | Adpar WwTW | BN0112801 | 535 | 1555 | Ceredigion | AFON TEIFI | 230496 | 240814 | 5 | 5 | 27 | 27 | Adpar WwTW | Dinmael STW
Afon Teifi/ River Teifi | BEULAH WWTW INLET SO BEULAH CERED'N | Beulah WwTW | BN0015801 | 109 | 534 | Ceredigion | NANT MEDINI | 229480 | 246160 | 5 | 2 | 27 | 27 | Beulah WwTW | Dolywern STW
Afon Teifi/ River Teifi | BLAENANNERCH STW | Blaenannerch STW | BH0052501 |  | 12.6 | Ceredigion | UNNAMED TRIB OF NANT ARBERTH | 224600 | 248690 | 8 | 8 | 27 | 27 | Blaenannerch STW | Erbistock STW
Afon Teifi/ River Teifi | BONCATH STW | Boncath STW | BG0001201 | 58.3 | 364 | Pembrokeshire | TRIBUTARY OF THE AFON MORGENAU | 220120 | 239040 | 5 | 5 | 27 | 27 | Boncath STW | Fenns Bank STW
Afon Teifi/ River Teifi | BRYNDULAIS STW LLANLWNI , | Bryndulais STW | BH0055602 | 17.45 | 52.36 | Carmarthenshire | UNNAMED TRIB AFON TEIFY | 249200 | 240200 | 8 | 8 | 27 | 27 | Bryndulais STW | Five Fords STW
Afon Teifi/ River Teifi | CAPEL IWAN STW | Capel Iwan STW | BN0054901 | 82 | 164 | Carmarthenshire | AFON MAMOG TRIB OF AFON CYCH | 229310 | 236040 | 5 | 1.8 | 27 | 27 | Capel Iwan STW | Four Crosses STW
Afon Teifi/ River Teifi | CARDIGAN WWTW(STW) CARDIGAN | Cardigan WwTW | BH0074101 | 2748 | 7603 | Ceredigion | AFON TEIFI | 217020 | 246140 | 8 | 8 | 27 | 27 | Cardigan WwTW | Froncysyllte STW
Afon Teifi/ River Teifi | Cellan Wastewater Treatment Works | Cellan WwTW | BN0008101 | 34.1 |  | Ceredigion | Afon Teifi | 260129 | 249105 | 5 | 5 | 27 | 27 | Cellan WwTW | Frongoch STW
Afon Teifi/ River Teifi | CENARTH WWTTW CENARTH CEREDIGION | Cenarth WwTW | BP0101201 | 152 | 818 | Ceredigion | AFON TEIFI | 226579 | 241662 | 5 | 5 | 27 | 27 | Cenarth WwTW | Glan Yr Afon STW
Afon Teifi/ River Teifi | CILGERRAN STW | Cilgerran STW | BP0217801 | 408 | 816 | Pembrokeshire | AFON TEIFI | 219480 | 243240 | 5 | 5 | 27 | 27 | Cilgerran STW | Glynceiriog STW
Afon Teifi/ River Teifi | Cribyn Wastewater treament works | Cribyn WwTW | BG0027001 | 34.1 |  | Ceredigion | Afon Grannell | 251542 | 251158 | 5 | 3.5 | 27 | 27 | Cribyn WwTW | Glyndyfrdwy WwTW
Afon Teifi/ River Teifi | CWRTNEWYDD STW CWRTNEWTDD | Cwrtnewydd STW | BN0005601 | 205 | 614 | Ceredigion | NANT CLEDYN | 249450 | 247100 | 5 | 5 | 27 | 27 | Cwrtnewydd STW | Grainnrhyd STW
Afon Teifi/ River Teifi | DANRHELYG STW NEWCASTLE EMLYN | Danrhelyg STW | BG0020001 |  | 5 | Carmarthenshire | TRIBUTARY OF AFON CYCH. | 229600 | 239700 | 8 | 8 | 27 | 27 | Danrhelyg STW | Gresford STW
Afon Teifi/ River Teifi | DREFACH/VELINDRE WWTW | Drefach/Velindre WwTW | BH0060601 | 943 |  | Carmarthenshire | AFON TEIFI | 235336 | 240291 | 5 | 5 | 27 | 27 | Drefach/Velindre WwTW | Halton WwTW
Afon Teifi/ River Teifi | FFOSTRASOL STW | Ffostrasol STW | BH0072801 | 31.8 | 190.9 | Ceredigion | AFON CERDIN FACH | 237800 | 247600 | 5 | 4.5 | 27 | 27 | Ffostrasol STW | Hanmer Arrowy STW
Afon Teifi/ River Teifi | GORSGOCH STW | Gorsgoch STW | BG0043501 | 18.6 | 56 | Ceredigion | UNNAMED TRIB OF AFON GRANNELL | 247600 | 250700 | 5 | 3 | 27 | 27 | Gorsgoch STW | Holt STW
Afon Teifi/ River Teifi | HENLLAN STW | Henllan STW | BN0013701 | 357 |  | Ceredigion | AFON TEIFI | 235355 | 240248 | 5 | 5 | 27 | 27 | Henllan STW | Hope WwTW
Afon Teifi/ River Teifi | LAMPETER STW LAMPETER | Lampeter STW | BP0045001 | 1201 |  | Ceredigion | RIVER TEIFI | 257630 | 247340 | 5 | 0.5 | 27 | 27 | Lampeter STW | Isycoed Marshlea STW
Afon Teifi/ River Teifi | LLANDEWI BREFI WWTW LLANDEWI BREFI | Llandewi Brefi WwTW | BG0023501 | 144 |  | Ceredigion | AFON BREFI | 265719 | 255183 | 1.5 | 1.5 | 27 | 27 | Llandewi Brefi WwTW | Lavister WwTW
Afon Teifi/ River Teifi | Llandysul Wastewater Treatment Works | Llandysul WwTW | BG0010201 | 689 |  | Carmarthenshire | RIVER TEIFI | 241910 | 240290 | 5 | 5 | 27 | 27 | Llandysul WwTW | Llanarmon Dc STW
Afon Teifi/ River Teifi | LLANFAIR CLYDOGAU WWTW CEREDIGION | Llanfair Clydogau WwTW | BH0070801 | 15 | 74 | Ceredigion | NANT CLYWEDOG | 262206 | 251252 | 8 | 8 | 27 | 27 | Llanfair Clydogau WwTW | Llanarmon-Yn-Ial STW
Afon Teifi/ River Teifi | LLANFIHANGEL-AR-ARTH STW | Llanfihangel-Ar-Arth STW | BN0020802 | 56.3 | 338 | Carmarthenshire | AFON TEIFI | 245490 | 240120 | 5 | 5 | 27 | 27 | Llanfihangel-Ar-Arth STW | Llandderfel WwTW
Afon Teifi/ River Teifi | LLANGYBI STW LLANGYBI LAMPETER | Llangybi STW | BG0021501 | 24 |  | Ceredigion | AFON DULAS | 260480 | 253020 | 5 | 5 | 27 | 27 | Llangybi STW | Llandrillo STW
Afon Teifi/ River Teifi | LLANYBYDDER WWTW CEREDIGION | Llanybydder WwTW | BJ0091401 | 1019 | 2376 | Carmarthenshire | AFON TEIFI | 251724 | 243265 | 5 | 2.5 | 27 | 27 | Llanybydder WwTW | Llanfihangel Glyn Myfyr STW
Afon Teifi/ River Teifi | LLECHRYD STW | Llechryd STW | BG0024901 | 138.3 |  | Ceredigion | AFON TEIFI | 221250 | 243340 | 5 | 5 | 27 | 27 | Llechryd STW | Llanfor STW
Afon Teifi/ River Teifi | NEWCHAPEL STW | Newchapel STW | BP0219501 | 46.6 | 218 | Pembrokeshire | UNNAMED TRIBUTARY OF THE AFON | 222470 | 239080 | 5 | 3.2 | 27 | 27 | Newchapel STW | Llanfynydd STW
Afon Teifi/ River Teifi | Package treatment plant (PTP) default | Package treatment plant (PTP) default | [7 empty] | 9.7 | 9.7 | 72.9 | 72.9 | Offer trin pecyn (PTP) rhagosodedig | Llangollen WwTW
Afon Teifi/ River Teifi | Package treatment plant (PTP) user defined | Package treatment plant (PTP) user defined | [11 empty] | Defnyddiwr offer trin pecyn (PTP) wedi'i ddiffinio | Llangower STW
Afon Teifi/ River Teifi | PENCADER STW | Pencader STW | BG0007801 | 439 | 1728 | Carmarthenshire | RIVER TYWELLI | 244600 | 236500 | 5 | 3.5 | 27 | 27 | Pencader STW | Llanuwchllyn STW
Afon Teifi/ River Teifi | PENTRECWRT STW | Pentrecwrt STW | BG0036101 | 56 |  | Carmarthenshire | AFON TEIFI | 238900 | 239100 | 5 | 5 | 27 | 27 | Pentrecwrt STW | Llidiart Annie STW
Afon Teifi/ River Teifi | Pontrhydfendigaid Wastewater Treatment Works | Pontrhydfendigaid WwTW | BN0040202 | 238.4 |  | Ceredigion | RIVER TEIFI | 272782 | 266709 | 5 | 1.8 | 27 | 27 | Pontrhydfendigaid WwTW | Maes Y Groes STW
Afon Teifi/ River Teifi | PONTRHYDYCEIRT STW LLWYNCELYN | Pontrhydyceirt STW | BG0023001 | 18.2 | 172.8 | Pembrokeshire | AFON MORGENNAU | 221100 | 242600 | 8 | 8 | 27 | 27 | Pontrhydyceirt STW | Min-Y-Rhos STW
Afon Teifi/ River Teifi | RHOSHILL STW RHOSHILL CARDIGAN | Rhoshill STW | BG0038101 | 10 |  | Pembrokeshire | NANT MORGENAU | 219300 | 240000 | 8 | 8 | 27 | 27 | Rhoshill STW | Mold WwTW
Afon Teifi/ River Teifi | RHOSYGADAIR NEWYDD BLAENANNERCH | Rhosygadair Newydd Blaenannerch | BP0302801 |  | 2.4 | Ceredigion | TRIB OF THE NANT ABERTH | 224582 | 249786 | 8 | 8 | 27 | 27 | Rhosygadair Newydd Blaenannerch | Overton WwTW
Afon Teifi/ River Teifi | RHYDLEWIS STW RHYDLEWIS LLANDYSSUL | Rhydlewis STW | BP0013501 | 66 | 280 | Ceredigion | NANT COLLEN | 234594 | 247314 | 5 | 4.5 | 27 | 27 | Rhydlewis STW | Package treatment plant (PTP) default
Afon Teifi/ River Teifi | Septic tank default | Septic tank default | [7 empty] | 11.6 | 11.6 | 96.3 | 96.3 | Tanc septig rhagosodedig | Package treatment plant (PTP) user defined
Afon Teifi/ River Teifi | Septic tank user defined | Septic tank user defined | [11 empty] | Defnyddiwr tanc septig wedi'i ddiffinio | Pandy STW
Afon Teifi/ River Teifi | TALGARREG WWTW TALGARREG CEREDIGION | Talgarreg WwTW | BG0011001 | 18 | 104 | Ceredigion | AFON CLETTWR | 242498 | 251050 | 8 | 3.5 | 27 | 27 | Talgarreg WwTW | Parc STW
Afon Teifi/ River Teifi | TREGARON WWTW TREGARON CEREDIGION | Tregaron WwTW | BH0057801 | 520.4 |  | Ceredigion | AFON TEIFI | 267261 | 259165 | 5 | 2 | 27 | 27 | Tregaron WwTW | Penley STW
Afon Teifi/ River Teifi | VERWIG STW VERWIG NR CARDIGAN DYFED | Verwig STW | BH0073801 | 37.7 | 138 | Ceredigion | NANT VERWIG | 218280 | 249420 | 8 | 8 | 27 | 27 | Verwig STW | Penrallt STW
Afon Tywi/ River Tywi | ABERGORLECH WWTW LLANDEILO CARMS | Abergorlech WwTW | BN0007002 | 25.7 |  | Carmarthenshire | AFON GORLECH | 258671 | 233790 | 5 | 5 | 27 | 27 | Abergorlech WwTW | Pentre Llyn Cymer STW
Afon Tywi/ River Tywi | ALLTWALIS STW | Alltwalis STW | BN0037001 |  | 19.9 | Carmarthenshire | NANT ALLTWALIS | 244300 | 231300 | 8 | 8 | 27 | 27 | Alltwalis STW | Pen-Y-Stryt WwTW
Afon Tywi/ River Tywi | BETHLEHEM STW BETHLEHEM LLANDEILO | Bethlehem STW | BJ0078601 | 12 |  | Carmarthenshire | AFON CEIDRYCH | 268186 | 225190 | 8 | 8 | 27 | 27 | Bethlehem STW | Pontfadog STW
Afon Tywi/ River Tywi | Brechfa Wastewater Treatment Works | Brechfa WwTW | BN0000302 | 43.6 |  | Carmarthenshire | Afon Marlais | 253050 | 230150 | 5 | 5 | 27 | 27 | Brechfa WwTW | Queensferry WwTW
Afon Tywi/ River Tywi | BRO DOLAU STW RHYDCYMERAU , | Bro Dolau STW | BP0226701 |  | 18 | Carmarthenshire | NANT MOELON | 257490 | 238950 | 8 | 8 | 27 | 27 | Bro Dolau STW | Rhosesmor STW
Afon Tywi/ River Tywi | BRO NANT STW NANTYFFIN BRECHFA | Bro Nant STW | BN0012701 | 15.3 | 91.6 | Carmarthenshire | NANT-Y-FFIN | 255500 | 232000 | 8 | 8 | 27 | 27 | Bro Nant STW | Rhyduchaf STW
Afon Tywi/ River Tywi | BROAD OAK WWTW FE BROAD OAK CARMS | Broad Oak WwTW | BJ0078701 | 10.9 | 76.7 | Carmarthenshire | NANT LASH | 257612 | 222336 | 8 | 8 | 27 | 27 | Broad Oak WwTW | Rhydymwyn STW
Afon Tywi/ River Tywi | BRONWYDD STW | Bronwydd STW | BP0211901 | 92 | 508 | Carmarthenshire | GWILI | 241820 | 223700 | 8 | 8 | 27 | 27 | Bronwydd STW | Sarnau STW
Afon Tywi/ River Tywi | BRYNGWYN WWTW GWYNFE RD LLANDEILO | Bryngwyn WwTW | BN0267201 | 6 | 39 | Carmarthenshire | AFON Y CWM | 267351 | 221995 | 8 | 8 | 27 | 27 | Bryngwyn WwTW | Septic tank default
Afon Tywi/ River Tywi | CAIO STW | Caio STW | BN0042101 | 21.8 | 65.4 | Carmarthenshire | AFON ANNELL | 267500 | 239600 | 5 | 5 | 27 | 27 | Caio STW | Septic tank user defined
Afon Tywi/ River Tywi | CILYCWM WWTW | Cilycwm WwTW | BH0050901 |  | 262 | Carmarthenshire | AFON GWENLAIS | 275450 | 239629 | 5 | 5 | 27 | 27 | Cilycwm WwTW | Tregeiriog STW
Afon Tywi/ River Tywi | CRUGYBAR STW CRUGYBAR LLANDEILO | Crugybar STW | BJ0076101 |  | 12 | Carmarthenshire | AFON ANNELL | 265580 | 237620 | 8 | 8 | 27 | 27 | Crugybar STW | Treuddyn (Bridge Terrace) STW
Afon Tywi/ River Tywi | Cwm Ifor Wastewater Treatment Works | Cwm Ifor WwTW | BN0103601 | 92.5 |  | Carmarthenshire | Afon Tywi | 266222 | 224935 | 5 | 5 | 27 | 27 | Cwm Ifor WwTW | Treuddyn Lodge Villas STW
Afon Tywi/ River Tywi | CWMDUAD STW | Cwmduad STW | BN0072901 | 33 |  | Carmarthenshire | AFON DUAD | 237796 | 230745 | 8 | 8 | 27 | 27 | Cwmduad STW | Treuddyn WwTW
Afon Tywi/ River Tywi | CWRT HENRI STW CWRT HENRI CARMS | Cwrt Henri STW | BN0018001 | 40.4 | 260 | Carmarthenshire | AFON DULAS | 255650 | 222700 | 5 | 5 | 27 | 27 | Cwrt Henri STW | Tryweryn Dam STW
Afon Tywi/ River Tywi | CYNGHORDY WWTW | Cynghordy WwTW | BJ0076001 | 22 |  | Carmarthenshire | RIVER BRAN | 280419 | 239810 | 5 | 5 | 27 | 27 | Cynghordy WwTW | Ty Gwyn WwTW
Afon Tywi/ River Tywi | CYNWYL ELFED WWTW CYNWYL ELFED CARM | Cynwyl Elfed WwTW | BG0028101 | 50 | 173 | Carmarthenshire | AFON DUAD | 237689 | 226996 | 8 | 8 | 27 | 27 | Cynwyl Elfed WwTW | Whitehurst STW
Afon Tywi/ River Tywi | FARMERS STW | Farmers STW | BN0077501 | 17 | 102 | Carmarthenshire | AFON TWRCH | 264800 | 244550 | 8 | 8 | 27 | 27 | Farmers STW | Worthenbury STW
Afon Tywi/ River Tywi | FELINGWM WASTEWATER TREATMENT WORKS | Felingwm WwTW | BJ0075601 | 22 |  | Carmarthenshire | NANT MYNACHDY | 250869 | 224399 | 5 | 5 | 27 | 27 | Felingwm WwTW
Afon Tywi/ River Tywi | FFAIRFACH STW | Ffairfach STW | BH0065401 | 847 | 2169 | Carmarthenshire | AFON TYWI | 261590 | 221170 | 5 | 5 | 27 | 27 | Ffairfach STW
Afon Tywi/ River Tywi | GLANYRAFON STW WHITEMILL CARMARTHE | Glanyrafon STW | BP0235101 |  | 9.3 | Carmarthenshire | AFON ANNELL | 246280 | 221570 | 8 | 8 | 27 | 27 | Glanyrafon STW
Afon Tywi/ River Tywi | GOLDEN GROVE WWTW LLANDEILO CARMS | Golden Grove WwTW | BJ0078801 | 10.08 | 92 | Carmarthenshire | THE AFON TOWY | 258919 | 221384 | 8 | 8 | 27 | 27 | Golden Grove WwTW
Afon Tywi/ River Tywi | GWYNFE STW CAPEL GWYNFE | Gwynfe STW | BP0164501 |  |  | Carmarthenshire | AFON CLYDACH | 272660 | 221760 | 8 | 8 | 27 | 27 | Gwynfe STW
Afon Tywi/ River Tywi | HEOL TIMOTHY STW FFALDYBRENIN | Heol Timothy STW | BN0045301 |  | 5 | Carmarthenshire | NANT CAMNANT | 263450 | 244250 | 8 | 8 | 27 | 27 | Heol Timothy STW
Afon Tywi/ River Tywi | LLANDOVERY WASTEWATER TREATMENT | Llandovery WwTW | BN0202701 | 705 | 1768 | Carmarthenshire | AFON BRAN | 276130 | 233180 | 5 | 5 | 27 | 27 | Llandovery WwTW
Afon Tywi/ River Tywi | LLANGADOG STW | Llangadog STW | BG0040001 | 427 |  | Carmarthenshire | RIVER SAWDDE | 269890 | 228140 | 5 | 5 | 27 | 27 | Llangadog STW
Afon Tywi/ River Tywi | LLANPUMPSAINT Wastewater treatment Worrks | Llanpumpsaint WwTW | BN0049101 | 317 |  | Carmarthenshire | Afon Gwili | 241540 | 229140 | 8 | 8 | 27 | 27 | Llanpumpsaint WwTW
Afon Tywi/ River Tywi | LLANSAWEL WWTW | Llansawel WwTW | BH0062601 | 57 | 147 | Carmarthenshire | AFON MARLAIS | 262395 | 236140 | 5 | 5 | 27 | 27 | Llansawel WwTW
Afon Tywi/ River Tywi | MYDDFAI WWTW MYDDFAI CARMARTHENSH | Myddfai WwTW | BH0050801 | 28 | 138 | Carmarthenshire | AFON BRAN | 277535 | 229762 | 5 | 5 | 27 | 27 | Myddfai WwTW
Afon Tywi/ River Tywi | Package treatment plant (PTP) default | Package treatment plant (PTP) default | [7 empty] | 9.7 | 9.7 | 72.9 | 72.9 | Offer trin pecyn (PTP) rhagosodedig
Afon Tywi/ River Tywi | Package treatment plant (PTP) user defined | Package treatment plant (PTP) user defined | [11 empty] | Defnyddiwr offer trin pecyn (PTP) wedi'i ddiffinio
Afon Tywi/ River Tywi | PONT-AR-GOTHI & NANTGAREDIG WWTW | Pont-Ar-Gothi & Nantgaredig WwTW | BN0002601 | 171 | 441 | Carmarthenshire | AFON COTHI | 250446 | 221217 | 5 | 5 | 27 | 27 | Pont-Ar-Gothi & Nantgaredig WwTW
Afon Tywi/ River Tywi | PUMPSAINT STW | Pumpsaint STW | BN0077401 | 16.5 |  | Carmarthenshire | AFON COTHI | 265851 | 240558 | 8 | 8 | 27 | 27 | Pumpsaint STW
Afon Tywi/ River Tywi | RHANDIRMWYN STW RHANDIRMWYN | Rhandirmwyn STW | BH0050701 |  |  | Carmarthenshire | AFON TYWI | 278000 | 243200 | 5 | 5 | 27 | 27 | Rhandirmwyn STW
Afon Tywi/ River Tywi | SALEM STW | Salem STW | BP0219002 | 56 | 113 | Carmarthenshire | AFON MYDDYFI | 262120 | 226640 | 5 | 5 | 27 | 27 | Salem STW
Afon Tywi/ River Tywi | Septic tank default | Septic tank default | [7 empty] | 11.6 | 11.6 | 96.3 | 96.3 | Tanc septig rhagosodedig
Afon Tywi/ River Tywi | Septic tank user defined | Septic tank user defined | [11 empty] | Defnyddiwr tanc septig wedi'i ddiffinio
Afon Tywi/ River Tywi | TALLEY WWTW LLANDEILO CARMS | Talley WwTW | BN0085301 | 128 | 426 | Carmarthenshire | NANT DDU | 264050 | 231782 | 5 | 5 | 27 | 27 | Talley WwTW
Afon Tywi/ River Tywi | TRAPP STW | Trapp STW | BJ0075101 | 3.3 |  | Carmarthenshire | RIVER CENNEN | 265360 | 218900 | 8 | 8 | 27 | 27 | Trapp STW
Afon Tywi/ River Tywi | TWYNLLANAN STW | Twynllanan STW | BP0164601 |  |  | Carmarthenshire | AFON SAWDE | 275380 | 224110 | 8 | 8 | 27 | 27 | Twynllanan STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | AMBLESTON STW | Ambleston STW | BG0001101 | 30.5 | 180 | Pembrokeshire | SPITTAL BROOK | 200370 | 225240 | 5 | 5 | 27 | 27 | Ambleston STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | BURTON FERRY STW | Burton Ferry STW | [5 empty] | 198042 | 204970 | 5 | 5 | 27 | 27 | BURTON FERRY STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | CAMROSE | Camrose | [5 empty] | 192488 | 220082 | 5 | 4.5 | 27 | 27 | CAMROSE
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Camrose Wastewater Treatment Works | Camrose WwTW | BG0004901 | 32 |  | Pembrokeshire | Camrose Brook | 192500 | 220040 | 5 | 4.5 | 27 | 27 | Camrose WwTW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | CAREW SWK | Carew STW | [5 empty] | 205182 | 203554 | 5 | 5 | 27 | 27 | CAREW SWK
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | CASTLEMORRIS WASTEWATER TREATMENT | Castlemorris Wastewater Treatment | BG0003501 | 16.8 | 82 | Pembrokeshire | Western Cleddau | 190488 | 231957 | 8 | 4 | 27 | 27 | Castlemorris Wastewater Treatment
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Clarbeston Wastewater Treatment Works | Clarbeston WwTW | BG0014501 | 84 |  | Pembrokeshire | CARTLETT BROOK | 201096 | 220967 | 5 | 1.5 | 27 | 27 | Clarbeston WwTW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | CLYNDERWEN STW | Clynderwen STW | BG0029501 | 182.8 |  | Pembrokeshire | PONT SHAN BROOK | 212390 | 218320 | 1 | 0.25 | 27 | 27 | Clynderwen STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | COSHESTON SWK | Cosheston STW | [5 empty] | 200147 | 203497 | 5 | 5 | 27 | 27 | COSHESTON SWK
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | HOOK | Hook STW | [5 empty] | 198479 | 211032 | 5 | 5 | 27 | 27 | HOOK
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | HUNDLETON SWK | Hundleton STW | [5 empty] | 196293 | 201333 | 5 | 5 | 27 | 27 | HUNDLETON SWK
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Keeston Wastewater Treatment Works | Keeston WwTW | BP0087901 | 129.2 |  | Pembrokeshire | Knock Brook | 190815 | 218678 | 5 | 1.5 | 27 | 27 | Keeston WwTW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | LAMPHEY STW | Lamphey STW | [5 empty] | 201911 | 200793 | 5 | 5 | 27 | 27 | LAMPHEY STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | LANGDON SWK | Langdon STW | [5 empty] | 210082 | 207451 | 5 | 5 | 27 | 27 | LANGDON SWK
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | LETTERSTON WEST STW | Letterston West STW | BH0071101 | 510 |  | Pembrokeshire | UNNAMED TRIB OF WESTERN CLEDDA | 192900 | 229150 | 5 | 2.5 | 27 | 27 | Letterston West STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | LLANDDEWI VELFREY STW | Llanddewi Velfrey STW | BG0013201 | 92 | 370 | Pembrokeshire | TRIBUTARY OF PONT-SHAN BROOK | 214210 | 216830 | 5 | 1 | 27 | 27 | Llanddewi Velfrey STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | LLANGOLMAN STW , ,. | Llangolman STW | BP0222601 |  | 6 | Pembrokeshire | UNNAMED TRIB OF EASTERN CLEDDA | 212640 | 227130 | 8 | 8 | 27 | 27 | Llangolman STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | LLANGWM SWK | Llangwm STW | [5 empty] | 199436 | 208777 | 5 | 5 | 27 | 27 | LLANGWM SWK
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | LLAWHADEN STW , , | Llawhaden STW | BH0071501 |  | 4.54 | Pembrokeshire | UNKNOWN TRIB OF EASTERN CLEDDA | 206800 | 217600 | 8 | 8 | 27 | 27 | Llawhaden STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | LLYS Y FRAN WWTW LLYS Y FRAN PEMBS | Llys Y Fran WwTW | BP0366401 | 14.5 |  | Pembrokeshire | AFON SYFYNWY | 203787 | 224195 | 8 | 8 | 27 | 27 | Llys Y Fran WwTW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | LLYSYFRAN RESERVOIR STW TEMPORARY O | Llysyfran Reservoir STW | BN0012901 |  | 4.09 | Pembrokeshire | TRIB. OF AFON SYFYNWY | 204000 | 224600 | 8 | 8 | 27 | 27 | Llysyfran Reservoir STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | MAENCLOCHOG STW CLYNDERWEN | Maenclochog STW | BG0000401 | 59.1 |  | Pembrokeshire | RIVER RHYDYFALLEN | 207537 | 226866 | 2 | 2 | 27 | 27 | Maenclochog STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | MATHRY STW NR FISHGUARD PEMBROKSHRE | Mathry STW | BG0009701 | 151 | 538 | Pembrokeshire | WESTERN CLEDDAU | 188339 | 231395 | 8 | 1 | 27 | 27 | Mathry STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | MERLINS BRIDGE | Merlins STW | [5 empty] | 195630 | 214640 | 5 | 5 | 27 | 27 | MERLINS BRIDGE
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | NARBERTH WEST swk | Narberth STW | [5 empty] | 210286 | 214257 | 5 | 5 | 27 | 27 | NARBERTH WEST swk
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | NEYLAND STW | Neyland STW | [5 empty] | 195782 | 205330 | 5 | 5 | 27 | 27 | NEYLAND STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Package treatment plant (PTP) default | Package treatment plant (PTP) default | [7 empty] | 9.7 | 9.7 | 72.9 | 72.9 | Offer trin pecyn (PTP) rhagosodedig
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Package treatment plant (PTP) default | Package treatment plant (PTP) default | [7 empty] | 9.7 | 9.7 | 72.9 | 72.9 | Offer trin pecyn (PTP) rhagosodedig
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Package treatment plant (PTP) user defined | Package treatment plant (PTP) user defined | [11 empty] | Defnyddiwr offer trin pecyn (PTP) wedi'i ddiffinio
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Package treatment plant (PTP) user defined | Package treatment plant (PTP) user defined | [11 empty] | Defnyddiwr offer trin pecyn (PTP) wedi'i ddiffinio
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | PANTEG STW | Panteg STW | BG0014001 | 15.3 |  | Pembrokeshire | UNNAMED TRIB OF AFON CLEDDAU | 192800 | 234800 | 8 | 0.8 | 27 | 27 | Panteg STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | PEMBROKE DOCK | Pembroke STW | [5 empty] | 195603 | 203765 | 1 | 1 | 27 | 27 | PEMBROKE DOCK
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | PUNCHESTON Wastewater Treatment Works | Puncheston WwTW | BG0017601 | 36.4 |  | Pembrokeshire | UNNAMED TRIB OF AFON ANGHOF | 200980 | 229830 | 5 | 5 | 27 | 27 | Puncheston WwTW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | REYNALTON SWK (NEW) | Reynalton STW | [5 empty] | 208886 | 208714 | 5 | 5 | 27 | 27 | REYNALTON SWK (NEW)
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | ROBESTON WATHEN HOUSING ACT WORKS | Robeston Wathen Housing Act Works | BP0232701 | 4.32 | 4.75 | Pembrokeshire | A TRIBUTARY OF PONT-SHAN BROOK | 208430 | 215940 | 8 | 8 | 27 | 27 | Robeston Wathen Housing Act Works
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | ROSEBUSH WwTW | Rosebush WwTW | BN0267001 | 22 |  | Pembrokeshire | Groundwater via infiltration system | 207329 | 229171 | 8 | 8 | 27 | 27 | Rosebush WwTW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | ROSEMARKET | Rosemarket STW | [5 empty] | 195371 | 207953 | 5 | 5 | 27 | 27 | ROSEMARKET
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Septic tank default | Septic tank default | [7 empty] | 11.6 | 11.6 | 96.3 | 96.3 | Tanc septig rhagosodedig
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Septic tank default | Septic tank default | [7 empty] | 11.6 | 11.6 | 96.3 | 96.3 | Tanc septig rhagosodedig
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Septic tank user defined | Septic tank user defined | [11 empty] | Defnyddiwr tanc septig wedi'i ddiffinio
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Septic tank user defined | Septic tank user defined | [11 empty] | Defnyddiwr tanc septig wedi'i ddiffinio
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | SPITTAL WWTW SPITTAL PEMBS | Spittal WwTW | BG0016901 | 81.4 | 384 | Pembrokeshire | TRIB OF RUDBAXTON WATER | 197348 | 222501 | 0.6 | 0.6 | 27 | 27 | Spittal WwTW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | TREFFGARNE STW | Treffgarne STW | BN0071601 |  |  | Pembrokeshire | WESTERN CLEDDAU | 195850 | 222950 | 5 | 5 | 27 | 27 | Treffgarne STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | UZMASTON SWK | Uzmaston STW | [5 empty] | 197233 | 214135 | 5 | 5 | 27 | 27 | UZMASTON SWK
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | WALTON EAST STW | Walton East STW | BN0083801 | 16.4 | 49.1 | Pembrokeshire | UNNAMED TRIB OF RIVER SYFYNWY | 202300 | 223000 | 8 | 8 | 27 | 27 | Walton East STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | WISTON STW HAVERFORDWEST , | Wiston STW | BP0257401 |  | 10 | Pembrokeshire | UNNAMED TRIBUTARY OF FENTON BR | 202620 | 217710 | 8 | 8 | 27 | 27 | Wiston STW
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | WOLFSCASTLE STW | Wolfscastle STW | BH0068601 | 77.3 | 463.6 | Pembrokeshire | AFON ANGHOF | 195800 | 226600 | 5 | 4.5 | 27 | 27 | Wolfscastle STW
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | CARMEL & PANTLLYN | Carmel STW | [5 empty] | 260084 | 217440 | 5 | 5 | 27 | 27 | CARMEL & PANTLLYN
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | CROSSHANDS SWK | Crosshands STW | [5 empty] | 256299 | 212335 | 1 | 1 | 27 | 27 | CROSSHANDS SWK
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | CWMGWILI | Cwmgwili STW | [5 empty] | 257728 | 210362 | 5 | 5 | 27 | 27 | CWMGWILI
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | CWMTAWEL | Cwmtawel STW | [5 empty] | 257098 | 211500 | 5 | 5 | 27 | 27 | CWMTAWEL
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | FELINDRE | Felindre STW | [5 empty] | 263232 | 202791 | 5 | 5 | 27 | 27 | FELINDRE
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | GARNSWLLT | Garnswllt STW | [5 empty] | 262143 | 209891 | 2 | 2 | 27 | 27 | GARNSWLLT
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | GOWERTON | Gowerton STW | [5 empty] | 259520 | 196904 | 1 | 1 | 15 | 15 | GOWERTON
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | LLANEDI | Llanedi STW | [5 empty] | 258190 | 207885 | 5 | 5 | 27 | 27 | LLANEDI
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | LLANELLI COASTAL | Llanelli STW | [5 empty] | 254120 | 198271 | 1 | 1 | 15 | 15 | LLANELLI COASTAL
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | LLANGENNECH | Llangennech STW | [5 empty] | 256739 | 201048 | 5 | 5 | 27 | 27 | LLANGENNECH
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | LLANNANT SWK | Llannant STW | [5 empty] | 257525 | 199837 | 5 | 5 | 27 | 27 | LLANNANT SWK
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | LLANNON | Llannon STW | [5 empty] | 254102 | 207802 | 5 | 5 | 27 | 27 | LLANNON
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | NANTGWINEU | Nantgwineu STW | [5 empty] | 269965 | 214171 | 5 | 5 | 27 | 27 | NANTGWINEU
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Package treatment plant (PTP) default | Package treatment plant (PTP) default | [7 empty] | 9.7 | 9.7 | 72.9 | 72.9 | Offer trin pecyn (PTP) rhagosodedig
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Package treatment plant (PTP) user defined | Package treatment plant (PTP) user defined | [11 empty] | Defnyddiwr offer trin pecyn (PTP) wedi'i ddiffinio
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | RHYD Y PANDY | Rhyd STW | [5 empty] | 266593 | 202087 | 5 | 5 | 27 | 27 | RHYD Y PANDY
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Septic tank default | Septic tank default | [7 empty] | 11.6 | 11.6 | 96.3 | 96.3 | Tanc septig rhagosodedig
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Septic tank user defined | Septic tank user defined | [11 empty] | Defnyddiwr tanc septig wedi'i ddiffinio
Bae Cemlyn/ Cemlyn Bay | Package treatment plant (PTP) default | Package treatment plant (PTP) default | [7 empty] | 9.7 | 9.7 | 72.9 | 72.9 | Offer trin pecyn (PTP) rhagosodedig
Bae Cemlyn/ Cemlyn Bay | Package treatment plant (PTP) user defined | Package treatment plant (PTP) user defined | [11 empty] | Defnyddiwr offer trin pecyn (PTP) wedi'i ddiffinio
Bae Cemlyn/ Cemlyn Bay | Septic tank default | Septic tank default | [7 empty] | 11.6 | 11.6 | 96.3 | 96.3 | Tanc septig rhagosodedig
Bae Cemlyn/ Cemlyn Bay | Septic tank user defined | Septic tank user defined | [11 empty] | Defnyddiwr tanc septig wedi'i ddiffinio
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | ABER (NANT GWYNANT) STW | Aber (Nant Gwynant) STW | CG0071301 |  |  | Gwynedd | AFON GLASLYN | 263220 | 351120 | 8 | 8 | 27 | 27 | Aber (Nant Gwynant) STW
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | BEDDGELERT WASTE WATER TREATMENT | Beddgelert WwTW | CG0024001 | 250.8 |  | Gwynedd | THE AFON GLASLYN | 259046 | 347618 | 5 | 5 | 27 | 27 | Beddgelert WwTW
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | CROESOR STW - NEW WORKS | Croesor STW | CG0133001 | 24.3 | 42.34 | Gwynedd | CROESOR | 262990 | 344590 | 5 | 5 | 27 | 27 | Croesor STW
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | LLANFROTHEN STW | Llanfrothen STW | CG0078701 | 57 |  | Gwynedd | RIVER CASEG | 260580 | 341600 | 5 | 5 | 27 | 27 | Llanfrothen STW
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | NANTMOR STW | Nantmor STW | CG0023901 |  |  | Gwynedd | GLASLYN | 259570 | 345640 | 8 | 8 | 27 | 27 | Nantmor STW
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Package treatment plant (PTP) default | Package treatment plant (PTP) default | [7 empty] | 9.7 | 9.7 | 72.9 | 72.9 | Offer trin pecyn (PTP) rhagosodedig
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Package treatment plant (PTP) user defined | Package treatment plant (PTP) user defined | [11 empty] | Defnyddiwr offer trin pecyn (PTP) wedi'i ddiffinio
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | PRENTEG STW | Prenteg STW | CG0015001 |  |  | Gwynedd | GLASLYN | 259300 | 341310 | 5 | 5 | 27 | 27 | Prenteg STW
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Septic tank default | Septic tank default | [7 empty] | 11.6 | 11.6 | 96.3 | 96.3 | Tanc septig rhagosodedig
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Septic tank user defined | Septic tank user defined | [11 empty] | Defnyddiwr tanc septig wedi'i ddiffinio
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | TOILET BLOCK PONT BETHANIA NANTGWY | Toilet Block Pont Bethania Nantgwy | CG0076201 |  | 5 | Gwynedd | AFON GLASLYN | 262660 | 350350 | 8 | 8 | 27 | 27 | Toilet Block Pont Bethania Nantgwy
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | ABENBURY WWTW | Abenbury WwTW | CM0110201 |  | 2.7 | Wrexham | RIVER CYLWEDOG | 336554 | 348403 | 8 | 8 | 27 | 27 | Abenbury WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | ALWEN SEPTIC TANK | Alwen Septic Tank | CP3021GW |  |  | Conwy | Groundwater via infiltration system | 296080 | 352603 | 8 | 8 | 27 | 27 | Alwen Septic Tank
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | BALA WWTW | Bala WwTW | CM0001501 | 689 | 1690 | Gwynedd | RIVER DEE | 293782 | 335551 | 5 | 4 | 27 | 27 | Bala WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | BANGOR ON DEE STW | Bangor On Dee STW | CM0060701 | 229 | 549 | Wrexham | RIVER DEE | 339500 | 346040 | 5 | 5 | 27 | 27 | Bangor On Dee STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | BETWS GWERFIL GOCH STW | Betws Gwerfil Goch STW | CM0026601 | 20.5 | 61.5 | Denbighshire | RIVER ALWEN | 303040 | 346310 | 5 | 5 | 27 | 27 | Betws Gwerfil Goch STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | BOWLING BANK STW FINAL EFFLUENT | Bowling Bank STW | CM0149401 |  |  | Wrexham | CLYWEDOG | 339900 | 348140 | 8 | 8 | 27 | 27 | Bowling Bank STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | BRONINGTON STW | Bronington STW | CM0072001 | 125 | 750 | Wrexham | UN-NAMED TRIB. OF ISCOED BROOK | 348650 | 340710 | 5 | 5 | 27 | 27 | Bronington STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | BRYNEGLWYS STW | Bryneglwys STW | CM0032401 | 34 |  | Denbighshire | RIVER MORWYNION | 314250 | 347250 | 5 | 5 | 27 | 27 | Bryneglwys STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Carrog Wastewater Treatment Works | Carrog WwTW | CM0000501 | 49 |  | Denbighshire | River Dee | 311740 | 343710 | 5 | 5 | 27 | 27 | Carrog WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | CEFN BRITH STW NR CERRIGYDRUDION | Cefn Brith STW | CG0328301 |  | 5 | Conwy | UN-NAMES WATERCOURSE AT CEFN B | 293330 | 350240 | 8 | 8 | 27 | 27 | Cefn Brith STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | CEFN MAWR WwTW | Cefn Mawr WwTW | CM0101301 | 1594 |  | Wrexham | RIVER DEE | 327450 | 341700 | 1 | 1 | 27 | 27 | Cefn Mawr WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | CERRIGYDRUDION STW | Cerrigydrudion STW | CM0052101 | 111 |  | Conwy | R NUG | 295258 | 348277 | 5 | 1 | 27 | 27 | Cerrigydrudion STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | CILCAIN PANTYMWYN STW | Cilcain Pantymwyn STW | CM0024401 | 241 | 1446 | Flintshire | ALYN | 319100 | 365500 | 8 | 5 | 27 | 27 | Cilcain Pantymwyn STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | CONNAHS QUAY STW | Connahs Quay STW | CM0037001 | 3898.3 |  | Flintshire | WEPRE BROOK | 330240 | 369380 | 8 | 8 | 27 | 27 | Connahs Quay STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | CORWEN WWTW FINAL EFFLUENT | Corwen WwTW | CM0018301 | 716.1 |  | Denbighshire | RIVER DEE | 308276 | 343573 | 1 | 1 | 27 | 27 | Corwen WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | CYNWYD STW FINAL EFFLUENT | Cynwyd STW | CM0149301 | 98.8 |  | Denbighshire | DEE | 305280 | 341130 | 5 | 5 | 27 | 27 | Cynwyd STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | DINMAEL STW | Dinmael STW | CM0038801 |  |  | Conwy | CEIRW | 300700 | 344700 | 8 | 8 | 27 | 27 | Dinmael STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | DOLYWERN STW | Dolywern STW | CM0007901 | 57.9 |  | Wrexham | RIVER CEILIOG | 322440 | 337250 | 5 | 2 | 27 | 27 | Dolywern STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | ERBISTOCK STW | Erbistock STW | CM0112101 |  |  | Wrexham | DEE | 335470 | 342030 | 8 | 8 | 27 | 27 | Erbistock STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | FENNS BANK STW | Fenns Bank STW | CM0095101 |  | 2 | Wrexham | RED BROOK | 351230 | 339010 | 8 | 8 | 27 | 27 | Fenns Bank STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | FIVE FORDS STW | Five Fords STW | CM0077801 | 27720 |  | Wrexham | RIVER DEE | 340900 | 347320 | 1 | 0.7 | 27 | 27 | Five Fords STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | FOUR CROSSES STW | Four Crosses STW | CM0190001 | 1.7 |  | Denbighshire | Groundwater via infiltration system | 303307 | 342927 | 8 | 8 | 27 | 27 | Four Crosses STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | FRONCYSYLLTE STW | Froncysyllte STW | CM0101501 | 114 | 381 | Wrexham | DEE | 327110 | 341960 | 5 | 5 | 27 | 27 | Froncysyllte STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | FRONGOCH STW | Frongoch STW | CM0077301 |  |  | Gwynedd | TRYWERYN | 290560 | 339120 | 5 | 5 | 27 | 27 | Frongoch STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | GLAN YR AFON STW | Glan Yr Afon STW | CM0045101 |  |  | Gwynedd | NANT FFRAUAR | 302460 | 342640 | 8 | 8 | 27 | 27 | Glan Yr Afon STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | GLYNCEIRIOG STW | Glynceiriog STW | CM0021801 | 124 |  | Wrexham | CEIRIOG | 320940 | 337830 | 5 | 0.5 | 27 | 27 | Glynceiriog STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Glyndyfrdwy Wastewater Treatment Works | Glyndyfrdwy WwTW | CM0026801 | 25.5 |  | Denbighshire | River Dee | 315270 | 342950 | 8 | 5 | 27 | 27 | Glyndyfrdwy WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | GRAINNRHYD STW | Grainnrhyd STW | CM0188501 | 10 |  | Denbighshire | UNNAMED TRIB OF RIVER TERRIG | 321520 | 356070 | 8 | 8 | 27 | 27 | Grainnrhyd STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | GRESFORD STW | Gresford STW | CM0040601 | 3590 |  | Wrexham | RIVER ALYN | 334880 | 355780 | 2 | 1 | 27 | 27 | Gresford STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | HALTON Wastewater Treatment Works | Halton WwTW | CM0022001 | 50 |  | Wrexham | RIVER DEE | 330582 | 340592 | 5 | 5 | 27 | 27 | Halton WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | HANMER ARROWY STW | Hanmer Arrowy STW | CM0095001 | 4.7 |  | Wrexham | TRIB OF EMRAL BROOK | 346130 | 338980 | 8 | 8 | 27 | 27 | Hanmer Arrowy STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | HOLT STW | Holt STW | CM0102001 | 210 |  | Wrexham | DEE | 340440 | 354810 | 5 | 5 | 27 | 27 | Holt STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | HOPE WwTW | Hope WwTW | CM0075801 | 2237 |  | Flintshire | ALYN | 330563 | 358092 | 1 | 1 | 27 | 27 | Hope WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | ISYCOED MARSHLEA STW | Isycoed Marshlea STW | CM0044801 | 1.8 |  | Wrexham | TRIB OF RIVER DEE | 339820 | 350820 | 8 | 8 | 27 | 27 | Isycoed Marshlea STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | LAVISTER WwTW | Lavister WwTW | CM0077501 | 1619 |  | Wrexham | PULFORD BROOK | 337715 | 358519 | 1 | 1 | 27 | 27 | Lavister WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | LLANARMON DC STW | Llanarmon Dc STW | CM0022101 |  |  | Wrexham | RIVER CEIRIOG | 315970 | 332870 | 5 | 1.5 | 27 | 27 | Llanarmon Dc STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | LLANARMON-YN-IAL STW | Llanarmon-Yn-Ial STW | CM0001201 | 64.5 | 295 | Denbighshire | RIVER ALYN | 319022 | 355938 | 5 | 5 | 27 | 27 | Llanarmon-Yn-Ial STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Llandderfel Wastewater Treatment Works | Llandderfel WwTW | CM0045201 | 22.7 |  | Gwynedd | Llandderfel Mill Stream | 298306 | 336993 | 5 | 5 | 27 | 27 | Llandderfel WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | LLANDRILLO STW | Llandrillo STW | CM0006001 | 71.3 |  | Denbighshire | RIVER CEIDIOG | 303550 | 337480 | 8 | 5 | 27 | 27 | Llandrillo STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | LLANFIHANGEL GLYN MYFYR STW | Llanfihangel Glyn Myfyr STW | CM0151001 |  |  | Conwy | ALWEN | 298960 | 349460 | 8 | 8 | 27 | 27 | Llanfihangel Glyn Myfyr STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | LLANFOR STW FINAL EFFLUENT | Llanfor STW | CM0160701 |  |  | Gwynedd | DEE | 294340 | 336560 | 8 | 8 | 27 | 27 | Llanfor STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | LLANFYNYDD STW | Llanfynydd STW | CM0011801 | 19 |  | Flintshire | RIVER CEGIDOG | 327620 | 356750 | 8 | 8 | 27 | 27 | Llanfynydd STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | LLANGOLLEN WWTW | Llangollen WwTW | CM0005401 | 1834 |  | Denbighshire | River Dee | 323413 | 342384 | 1 | 1 | 27 | 27 | Llangollen WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | LLANGOWER STW | Llangower STW | CM0066201 |  |  | Gwynedd | AFON GLYN | 290440 | 332340 | 8 | 8 | 27 | 27 | Llangower STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | LLANUWCHLLYN STW LLANUWCHLLYN | Llanuwchllyn STW | CM0000801 | 363.2 |  | Gwynedd | THE AFON TWRCH | 288098 | 330300 | 2 | 2 | 27 | 27 | Llanuwchllyn STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | LLIDIART ANNIE STW | Llidiart Annie STW | CM0013201 |  | 36.8 | Denbighshire | DEE | 318774 | 344519 | 8 | 8 | 27 | 27 | Llidiart Annie STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | MAES Y GROES STW | Maes Y Groes STW | CM0071201 | 523 | 3138 | Flintshire | ALYN | 319190 | 363490 | 5 | 5 | 27 | 27 | Maes Y Groes STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | MIN-Y-RHOS STW | Min-Y-Rhos STW | CM0027201 |  |  | Denbighshire | MORWYNION | 314690 | 347440 | 8 | 8 | 27 | 27 | Min-Y-Rhos STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | MOLD WwTW | Mold WwTW | CM0031001 | 4125 |  | Flintshire | UN-NAMED TRIB OF THE RIVER ALYN | 324750 | 363140 | 1 | 1 | 27 | 27 | Mold WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | OVERTON WWTW | Overton WwTW | CM0188601 | 257.2 | 688.6 | Wrexham | RIVER DEE | 336620 | 341597 | 5 | 5 | 27 | 27 | Overton WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Package treatment plant (PTP) default | Package treatment plant (PTP) default | [7 empty] | 9.7 | 9.7 | 72.9 | 72.9 | Offer trin pecyn (PTP) rhagosodedig
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Package treatment plant (PTP) user defined | Package treatment plant (PTP) user defined | [11 empty] | Defnyddiwr offer trin pecyn (PTP) wedi'i ddiffinio
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | PANDY STW | Pandy STW | CM0022201 |  |  | Wrexham | CEIRIOG | 319680 | 335880 | 5 | 5 | 27 | 27 | Pandy STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | PARC STW | Parc STW | CM0055301 |  |  | Gwynedd | LLANFAR | 287740 | 333880 | 8 | 8 | 27 | 27 | Parc STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | PENLEY STW | Penley STW | CM0118501 | 182 | 546 | Wrexham | UN-NAMED TRIB. OF EMRAL BROOK | 341480 | 340460 | 5 | 0.9 | 27 | 27 | Penley STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | PENRALLT STW | Penrallt STW | CM0190201 | 7 |  | Denbighshire | Groundwater via infiltration system | 314400 | 342796 | 8 | 8 | 27 | 27 | Penrallt STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | PENTRE LLYN CYMER STW | Pentre Llyn Cymer STW | CM0095501 |  |  | Conwy | ALWEN | 297380 | 352850 | 8 | 8 | 27 | 27 | Pentre Llyn Cymer STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Pen-y-stryt Wastewater Treatment Works | Pen-Y-Stryt WwTW | CM0043501 | 36 |  | Denbighshire | River Alyn | 319535 | 351809 | 5 | 5 | 27 | 27 | Pen-Y-Stryt WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | PONTFADOG STW | Pontfadog STW | CM0021701 |  |  | Wrexham | CEIRIOG | 324170 | 338440 | 5 | 1 | 27 | 27 | Pontfadog STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | QUEENSFERRY WWTW | Queensferry WwTW | CM0082201 | 11067.9 |  | Flintshire | RIVER DEE ESTUARY | 332379 | 368522 | 8 | 8 | 27 | 27 | Queensferry WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | RHOSESMOR STW | Rhosesmor STW | CM0044201 | 174 |  | Flintshire | UNNAMED TRIB.OF DOLFECHLAS BRO | 321000 | 368150 | 5 | 5 | 27 | 27 | Rhosesmor STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | RHYDUCHAF STW | Rhyduchaf STW | CM0045401 |  |  | Gwynedd | NANT ABERDULDOG | 290250 | 337950 | 8 | 8 | 27 | 27 | Rhyduchaf STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | RHYDYMWYN STW | Rhydymwyn STW | CM0004201 | 192 |  | Flintshire | DOLFECHLAS BROOK | 320900 | 366500 | 8 | 5 | 27 | 27 | Rhydymwyn STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | SARNAU SEWAGE TREATMENT WORKS | Sarnau STW | CM0094501 | 3.95 |  | Gwynedd | CORS SARNAU | 297110 | 339340 | 8 | 1.8 | 27 | 27 | Sarnau STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Septic tank default | Septic tank default | [7 empty] | 11.6 | 11.6 | 96.3 | 96.3 | Tanc septig rhagosodedig
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Septic tank user defined | Septic tank user defined | [11 empty] | Defnyddiwr tanc septig wedi'i ddiffinio
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | TREGEIRIOG STW | Tregeiriog STW | CM0021901 |  |  | Wrexham | CEIRIOG | 317930 | 333630 | 8 | 4 | 27 | 27 | Tregeiriog STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | TREUDDYN (BRIDGE TERRACE) STW | Treuddyn (Bridge Terrace) STW | CM0116701 |  | 2.5 | Flintshire | BYR BROOK | 325520 | 357930 | 8 | 8 | 27 | 27 | Treuddyn (Bridge Terrace) STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | TREUDDYN LODGE VILLAS STW | Treuddyn Lodge Villas STW | CM0027701 |  | 3.4 | Flintshire | UN-NAMED TRIB OF BYR BROOK | 326330 | 358220 | 8 | 8 | 27 | 27 | Treuddyn Lodge Villas STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Treuddyn Wastewater Treatment Works | Treuddyn WwTW | CM0066101 | 275 |  | Flintshire | UN-NAMED TRIB. OF BYR BROOK | 325669 | 357978 | 5 | 5 | 27 | 27 | Treuddyn WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | TRYWERYN DAM STW | Tryweryn Dam STW | CM0010801 |  |  | Gwynedd | TRYWERYN | 288300 | 339900 | 8 | 8 | 27 | 27 | Tryweryn Dam STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | TY GWYN WWTW BUCKLEY | Ty Gwyn WwTW | CM0081001 | 4061 |  | Flintshire | BLACK BROOK | 327890 | 362220 | 1 | 1 | 27 | 27 | Ty Gwyn WwTW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | WHITEHURST STW | Whitehurst STW | CM0094201 |  |  | Wrexham | AFON BRADLEY | 329050 | 340030 | 8 | 8 | 27 | 27 | Whitehurst STW
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | WORTHENBURY STW | Worthenbury STW | CM0001301 |  | 10.8 | Wrexham | UN-NAMED TRIB OF EMRAL BROOK | 342100 | 345900 | 8 | 8 | 27 | 27 | Worthenbury STW
River Usk/ Afon Wysg | ABER STW | Aber STW | AA0026701 |  | 4 | Powys | NANT-CLYDACH | 310580 | 221480 | 5 | 5 | 27 | 27 | Aber STW
River Usk/ Afon Wysg | ABERBAIDEN STW BEHIND HOP YARD FARM | Aberbaiden STW | AB0034101 | 1535 | 3615 | Monmouthshire | THE RIVER USK | 326346 | 214778 | 5 | 5 | 27 | 27 | Aberbaiden STW
River Usk/ Afon Wysg | BRECON STW BRECON WWTW BRECON POWYS | Brecon STW | AB0041501 | 2887 | 6794 | Powys | RIVER USK | 305921 | 227595 | 5 | 2 | 27 | 27 | Brecon STW
River Usk/ Afon Wysg | Bryn Wastewater Treatment Works | Bryn WwTW | AA0017501 | 83 |  | Monmouthshire | River Usk | 333382 | 209730 | 5 | 5 | 27 | 27 | Bryn WwTW
River Usk/ Afon Wysg | BRYNMAWR STW BLACKROCK BRYNMAWR | Brynmawr STW | AC0085601 | 1918 | 4476 | Blaenau Gwent | RIVER CLYDACH | 320805 | 212409 | 1 | 8 | 27 | 27 | Brynmawr STW
River Usk/ Afon Wysg | BWLCH (S) STW LLANGYNIDIR | Bwlch (S) STW | AB0049501 | 378.5 |  | Powys | RIVER USK | 315500 | 220300 | 5 | 5 | 27 | 27 | Bwlch (S) STW
River Usk/ Afon Wysg | CAERLEON ROAD STW 562 - 574 CAERLEO | Caerleon Road STW | AN0214001 | 5.6 |  | Newport | UN-NAMED TRIB. OF R. USK | 333720 | 189530 | 8 | 8 | 27 | 27 | Caerleon Road STW
River Usk/ Afon Wysg | Christchurch Wastewater Treatment Works | Christchurch WwTW | AB0050201 | 47.5 |  | Newport | Usk Estuary | 333940 | 189768 | 5 | 8 | 27 | 27 | Christchurch WwTW
River Usk/ Afon Wysg | COEDWAUNGAER STW SENNYBRIDGE , | Coedwaungaer STW | AB0043501 |  | 26.4 | Powys | USK RIVER | 292550 | 229380 | 5 | 8 | 27 | 27 | Coedwaungaer STW
River Usk/ Afon Wysg | CRADOC S T W PHASE 1 | Cradoc STW | AN0035901 |  |  | Powys | AFON YSCIR | 300378 | 230142 | 5 | 8 | 27 | 27 | Cradoc STW
River Usk/ Afon Wysg | CRAY STW CRAY BRECON POWYS | Cray STW | AD0000701 | 13 |  | Powys | NANT DDU | 289750 | 224370 | 8 | 8 | 27 | 27 | Cray STW
River Usk/ Afon Wysg | CRICKHOWELL STW ABERGAVENNY ROAD | Crickhowell STW | AC0094701 | 811.6 |  | Powys | THE RIVER USK | 322506 | 217473 | 5 | 5 | 27 | 27 | Crickhowell STW
River Usk/ Afon Wysg | CWMDU STW CRICKHOWELL , | Cwmdu STW | AC0098201 |  | 10 | Powys | RHION GOLL | 317850 | 223300 | 8 | 8 | 27 | 27 | Cwmdu STW
River Usk/ Afon Wysg | DAN Y PARC HIGHWAYS DEPOT STW , , | Dan Y Parc Highways Depot STW | AN0261301 |  | 0.15 | Powys | NANT WENLLAN | 322150 | 217000 | 8 | 8 | 27 | 27 | Dan Y Parc Highways Depot STW
River Usk/ Afon Wysg | DEVAUDEN STW | Devauden STW | AA0001901 | 58 | 348 | Monmouthshire | TRIBUTARY OF PILL BROOK | 347270 | 198860 | 5 | 5 | 27 | 27 | Devauden STW
River Usk/ Afon Wysg | GLANGRWYNEY STW , , | Glangrwyney STW | AA0000701 |  | 1.35 | Monmouthshire | RIVER USK | 324100 | 216200 | 8 | 8 | 27 | 27 | Glangrwyney STW
River Usk/ Afon Wysg | GOYTRE SEWAGE TREATMENT WORKS NANT | Goytre STW | AC0116401 | 384 | 957 | Monmouthshire | USK RIVER | 334455 | 205405 | 5 | 1.4 | 27 | 27 | Goytre STW
River Usk/ Afon Wysg | GREAT OAK STW GREAT OAK MONMOUTH | Great Oak STW | AA0027601 | 12.3 | 24 | Monmouthshire | TRIBNUTARY OF CLAWDD BROOK | 338340 | 210160 | 8 | 5 | 27 | 27 | Great Oak STW
River Usk/ Afon Wysg | GROESFFORDD STW | Groesffordd STW | AD0018101 | 36 | 108 | Powys | BRYNICH BROOK | 307370 | 227580 | 5 | 5 | 27 | 27 | Groesffordd STW
River Usk/ Afon Wysg | GWERNESNEY STW , , | Gwernesney STW | AB0058501 | 7.2 | 22 | Monmouthshire | TRIBUTARY OF OLWAY BROOK | 340800 | 201920 | 8 | 8 | 27 | 27 | Gwernesney STW
River Usk/ Afon Wysg | LIBANUS Wastewater Treatment Works | Libanus WwTW | AB0076001 | 114 |  | Powys | RIVER TARELL | 299780 | 226036 | 5 | 2 | 27 | 27 | Libanus WwTW
River Usk/ Afon Wysg | LITTLE MILL STW MONKSWOOD USK | Little Mill STW | AD0002501 | 82 | 246 | Monmouthshire | BERTHIN BROOK | 333750 | 202400 | 5 | 5 | 27 | 27 | Little Mill STW
River Usk/ Afon Wysg | LLANARTH STW LLANARTH MONMOUTHSHI | Llanarth STW | AC0091901 | 50 | 228 | Monmouthshire | TRIBUTARY OF CLAWDD BROOK | 337783 | 210477 | 5 | 5 | 27 | 27 | Llanarth STW
River Usk/ Afon Wysg | Llanbedr Wastewater Treatment Works | Llanbedr WwTW | AA0003101 | 39 |  | Powys | TRIBUTARY OF RIVER GRWYNE | 323819 | 220066 | 5 | 1 | 27 | 27 | Llanbedr WwTW
River Usk/ Afon Wysg | LLANDDEW STW LLANDDEW BRECON | Llanddew STW | AC0140701 | 21 |  | Powys | NANT ANOD | 305130 | 230830 | 5 | 4 | 27 | 27 | Llanddew STW
River Usk/ Afon Wysg | LLANDEGFEDD (WAUNYPWLL) STW , , | Llandegfedd (Waunypwll) STW | AD0002601 |  | 4 | Monmouthshire | SOR BROOK | 334000 | 195350 | 8 | 8 | 27 | 27 | Llandegfedd (Waunypwll) STW
River Usk/ Afon Wysg | LLANELLEN STW LLANELLEN MONMOUTHSHE | Llanellen STW | AB0046101 | 107.5 |  | Monmouthshire | RIVER USK | 330300 | 211150 | 5 | 5 | 27 | 27 | Llanellen STW
River Usk/ Afon Wysg | LLANFIHANGLE NANT BRAN STW | Llanfihangle Nant Bran STW | AA0015101 |  |  | Powys | NANT BRAN STREAM | 294380 | 234150 | 8 | 8 | 27 | 27 | Llanfihangle Nant Bran STW
River Usk/ Afon Wysg | LLANFOIST WASTEWATER TREATMENT WORKS ME | Llanfoist WwTW | AB0038201 | 5723 | 11805 | Monmouthshire | RIVER USK | 330082 | 213206 | 5 | 2 | 27 | 27 | Llanfoist WwTW
River Usk/ Afon Wysg | LLANFYRNACH STW LLANFYRNACH , | Llanfyrnach STW | AD0002101 | 32.7 | 98 | Powys | NANT MENASCIN | 307850 | 225830 | 8 | 2.5 | 27 | 27 | Llanfyrnach STW
River Usk/ Afon Wysg | LLANGENNY STW , , | Llangenny STW | AC0141001 |  | 3.2 | Powys | RIVER GRWYNE | 324050 | 217920 | 8 | 8 | 27 | 27 | Llangenny STW
River Usk/ Afon Wysg | LLANGYBI STW LLANGYBI USK | Llangybi STW | AB0046601 | 204 | 456 | Monmouthshire | RIVER USK | 338477 | 196090 | 5 | 5 | 27 | 27 | Llangybi STW
River Usk/ Afon Wysg | LLANISHEN STW LLANISHEN MONMOUTHSHE | Llanishen STW | AD0004201 |  |  | Monmouthshire | TRIBUTARY OF OLWAY BROOK | 347650 | 203090 | 8 | 8 | 27 | 27 | Llanishen STW
River Usk/ Afon Wysg | LLANOVER STW LLANOVER MONMOUTHSHIE | Llanover STW | AB0043401 | 86.6 |  | Monmouthshire | RIVER USK | 331950 | 209360 | 5 | 5 | 27 | 27 | Llanover STW
River Usk/ Afon Wysg | LLANSOY STW CHURCH LANE LLANSOY | Llansoy STW | AN0106401 | 16.2 | 138 | Monmouthshire | PILL BROOK | 343816 | 202047 | 8 | 8 | 27 | 27 | Llansoy STW
River Usk/ Afon Wysg | LLANSPYDDID STW | Llanspyddid STW | AB0056601 | 23.7 | 54 | Powys | RIVER USK TRIBUTARY | 301090 | 228290 | 5 | 5 | 27 | 27 | Llanspyddid STW
River Usk/ Afon Wysg | LLANVAIR STW LLANVAIR MONMOUTHSHIRE | Llanvair STW | AD0001501 | 44.5 | 134 | Monmouthshire | RIVER USK | 335000 | 206770 | 5 | 5 | 27 | 27 | Llanvair STW
River Usk/ Afon Wysg | Llanwenarth Sewage Treatment Works | Llanwenarth STW | AD0010501 | 5 |  | Monmouthshire | UN-NAMED TRIBUTARY OF RIVER US | 328180 | 214810 | 8 | 8 | 27 | 27 | Llanwenarth STW
River Usk/ Afon Wysg | NASH STW WEST NASH ROAD NEWPORT | Nash STW | AB0067101 | 57900 | 122256 | Newport | JULIANS PILL | 333450 | 184110 | 8 | 8 | 27 | 27 | Nash STW
River Usk/ Afon Wysg | Package treatment plant (PTP) default | Package treatment plant (PTP) default | [7 empty] | 9.7 | 9.7 | 72.9 | 72.9 | Offer trin pecyn (PTP) rhagosodedig
River Usk/ Afon Wysg | Package treatment plant (PTP) user defined | Package treatment plant (PTP) user defined | [11 empty] | Defnyddiwr offer trin pecyn (PTP) wedi'i ddiffinio
River Usk/ Afon Wysg | PANTYGASSEG WASTEWATER SEWAGE WORKS | Pantygasseg WwTW | AN0098001 | 19.3 |  | Torfaen | Groundwater via infiltration system | 325109 | 199905 | 8 | 8 | 27 | 27 | Pantygasseg WwTW
River Usk/ Afon Wysg | PENCELLI STW PENCELLI POWYS | Pencelli STW | AD0010801 |  |  | Powys | NANT MENASCIN | 309320 | 225340 | 8 | 8 | 27 | 27 | Pencelli STW
River Usk/ Afon Wysg | PENNORTH AND SCETHROG STW USK | Pennorth And Scethrog STW | AA0002301 |  |  | Powys | RIVER USK | 310650 | 224850 | 8 | 8 | 27 | 27 | Pennorth And Scethrog STW
River Usk/ Afon Wysg | PONTFAEN STW , , | Pontfaen STW | AA0015001 |  | 0.8 | Powys | AFON YSGIR FAWR | 299650 | 234100 | 8 | 8 | 27 | 27 | Pontfaen STW
River Usk/ Afon Wysg | PONTHIR STW PONTHIR NEWPORT | Ponthir STW | AB0064101 | 32946 | 76550 | Newport | USK ESTUARY | 334660 | 190430 | 8 | 8 | 27 | 27 | Ponthir STW
River Usk/ Afon Wysg | RAGLAN ENTERPRISE PARK RAGLAN | Raglan Enterprise Park | AD0004101 |  | 2 | Monmouthshire | NANT Y WILCAE | 341400 | 207200 | 8 | 8 | 27 | 27 | Raglan Enterprise Park
River Usk/ Afon Wysg | RAGLAN STW CHEPSTOW ROAD RAGLAN | Raglan STW | AC0140201 | 470 | 1194 | Monmouthshire | THE NANT Y WILCAE | 341637 | 207143 | 1 | 8 | 27 | 27 | Raglan STW
River Usk/ Afon Wysg | SENNYBRIDGE ARMY CAMP STW | Sennybridge Army Camp STW | AC0140301 |  | 451 | Powys | RIVER USK | 292530 | 229450 | 5 | 3.5 | 27 | 27 | Sennybridge Army Camp STW
River Usk/ Afon Wysg | Septic tank default | Septic tank default | [7 empty] | 11.6 | 11.6 | 96.3 | 96.3 | Tanc septig rhagosodedig
River Usk/ Afon Wysg | Septic tank user defined | Septic tank user defined | [11 empty] | Defnyddiwr tanc septig wedi'i ddiffinio
River Usk/ Afon Wysg | STP @ CROSS OAK | STP @ Cross Oak | AN0178801 |  | 3.2 | Powys | Groundwater via infiltration system | 310663 | 223911 | 8 | 8 | 27 | 27 | STP @ Cross Oak
River Usk/ Afon Wysg | STW AT LOWER CHAPEL BRECON , | STW At Lower Chapel Brecon , | AN0273701 |  | 4.4 | Powys | RIVER HONDDU | 302740 | 235730 | 8 | 8 | 27 | 27 | STW At Lower Chapel Brecon ,
River Usk/ Afon Wysg | STW SERVING COURT FARM WTW | STW Serving Court Farm Wtw | AA0032001 |  | 2 | Monmouthshire | UNNAMED TRIB OF AFON LWYD | 333720 | 193410 | 8 | 8 | 27 | 27 | STW Serving Court Farm Wtw
River Usk/ Afon Wysg | TALYBONT SEWAGE TREATMENT WORKS TAL | Talybont STW | AD0001701 | 89 | 226 | Powys | RIVER CAERFANELL | 312069 | 223056 | 5 | 1 | 27 | 27 | Talybont STW
River Usk/ Afon Wysg | Trecastle Wastewater Treatment Works | Trecastle WwTW | AD0000901 | 46 |  | Powys | Nant Logyn | 288022 | 228859 | 5 | 0.75 | 27 | 27 | Trecastle WwTW
River Usk/ Afon Wysg | TREDUNNOCK STW VIA LITTLE TON FARM | Tredunnock STW | AA0001501 | 18 | 151 | Monmouthshire | USK RIVER TRIBUTARY | 337795 | 194495 | 8 | 8 | 27 | 27 | Tredunnock STW
River Usk/ Afon Wysg | TRELLECH STW | Trellech STW | AN0214601 | 9 | 54 | Monmouthshire | OLWAY BROOK | 349900 | 205500 | 5 | 8 | 27 | 27 | Trellech STW
River Usk/ Afon Wysg | TRETOWER STW TRETOWER CRICKHOWELL | Tretower STW | AN0106601 |  |  | Powys | RHIAN GOLL | 318900 | 220870 | 8 | 8 | 27 | 27 | Tretower STW
River Usk/ Afon Wysg | USK STW GRAIG OLWAY FARM LLANGVIEW | Usk STW | AB0044801 | 579 | 3110 | Monmouthshire | RIVER USK | 338680 | 199449 | 5 | 5 | 27 | 27 | Usk STW
River Wye/ Afon Gwy | ABBEYCWMHIR WWTW | Abbeycwmhir WwTW | AN0178601 | 15 |  | Powys | Groundwater via infiltration system | 305531 | 270993 | 8 | 8 | 27 | 27 | Abbeycwmhir WwTW
River Wye/ Afon Gwy | ABEREDW STW | Aberedw STW | AW1000101 | 14 |  | Powys | EDW RIVER | 307600 | 247400 | 8 | 8 | 27 | 27 | Aberedw STW
River Wye/ Afon Gwy | ABERLLYNFI THREE COCKS | Aberllynfi Three Cocks | AW1000301 | 66 | 169 | Powys | TREGOYD BROOK | 317400 | 237800 | 5 | 3.5 | 27 | 27 | Aberllynfi Three Cocks
River Wye/ Afon Gwy | BEULAH STW BEULAH POWYS WALES | Beulah STW | AW1000501 | 54 |  | Powys | THE RIVER CAMMARCH | 292221 | 251039 | 5 | 3 | 27 | 27 | Beulah STW
River Wye/ Afon Gwy | BUILTH ROAD STW | Builth Road STW | AW1000601 | 26 |  | Powys | DULAS BROOK | 302140 | 253090 | 5 | 3 | 27 | 27 | Builth Road STW
River Wye/ Afon Gwy | BUILTH WELLS STW | Builth Wells STW | AW1000701 | 1622 |  | Powys | WYE RIVER | 304552 | 251471 | 2.5 | 2.5 | 27 | 27 | Builth Wells STW
River Wye/ Afon Gwy | Cefn Gorwydd Wastewater Treatment Works | Cefn Gorwydd WwTW | AN0180001 | 20 |  | Powys | River Irfon | 289912 | 245976 | 5 | 8 | 27 | 27 | Cefn Gorwydd WwTW
River Wye/ Afon Gwy | CILMERY STW | Cilmery STW | AW1001001 | 23 | 69 | Powys | AFON CHWEFRU | 300800 | 251800 | 5 | 4 | 27 | 27 | Cilmery STW
River Wye/ Afon Gwy | Clyro Wastewater Treatment Works | Clyro WwTW | AW1000901 | 33.6 |  | Powys | Clyro Brook | 321702 | 243836 | 5 | 5 | 27 | 27 | Clyro WwTW
River Wye/ Afon Gwy | CROSSGATES STW | Crossgates STW | AW1001101 | 245.6 |  | Powys | RIVER ITHON | 308660 | 264240 | 5 | 2 | 27 | 27 | Crossgates STW
River Wye/ Afon Gwy | CWMYOY STW | Cwmyoy STW | AH1000501 |  | 3.6 | Monmouthshire | AFON HONDDU | 331190 | 221600 | 8 | 8 | 27 | 27 | Cwmyoy STW
River Wye/ Afon Gwy | DINGESTOW STW DINGESTOW MONMOUTH | Dingestow STW | AS1000701 |  |  | Monmouthshire | TROTHY RIVER | 345890 | 210050 | 8 | 5 | 27 | 27 | Dingestow STW
River Wye/ Afon Gwy | ELAN GLAN-YR-AFON STW | Elan Glan-Yr-Afon STW | AN0179501 |  | 3.2 | Powys | Groundwater via infiltration system | 293476 | 265384 | 8 | 8 | 27 | 27 | Elan Glan-Yr-Afon STW
River Wye/ Afon Gwy | ELAN VILLAGE STW | Elan Village STW | AW1001401 |  | 71 | Powys | ELAN | 293570 | 265360 | 8 | 8 | 27 | 27 | Elan Village STW
River Wye/ Afon Gwy | ERWOOD STW ERWOOD BUILTH WELLS | Erwood STW | AW1001501 |  |  | Powys | WYE | 310000 | 243290 | 8 | 8 | 27 | 27 | Erwood STW
River Wye/ Afon Gwy | EVENJOBB STW PRESTEIGNE POWYS | Evenjobb STW | AN0179601 |  | 3.8 | Powys | Groundwater via infiltration system | 326357 | 262270 | 8 | 8 | 27 | 27 | Evenjobb STW
River Wye/ Afon Gwy | FFORDDLAS STW | Fforddlas STW | AN0179701 |  | 13.2 | Powys | Groundwater via infiltration system | 320107 | 238687 | 8 | 8 | 27 | 27 | Fforddlas STW
River Wye/ Afon Gwy | GARTH STW | Garth STW | AW1002001 | 27.3 | 164 | Powys | DULAS BROOK | 295200 | 249400 | 5 | 5 | 27 | 27 | Garth STW
River Wye/ Afon Gwy | GLASBURY STW GLASBURY NR HAY ON WYE | Glasbury STW | AN0333401 | 475 | 950 | Powys | THE RIVER WYE | 317936 | 239549 | 8 | 8 | 27 | 27 | Glasbury STW
River Wye/ Afon Gwy | GREAT CRAIG CROSS ASH STW | Great Craig Cross Ash STW | AS1001201 | 12.4 | 107 | Monmouthshire | LLWYNON BROOK | 340570 | 220093 | 8 | 8 | 27 | 27 | Great Craig Cross Ash STW
River Wye/ Afon Gwy | Grosmont Wastewater Treatment Works | Grosmont WwTW | AH1001001 | 38 |  | Monmouthshire | River Monnow | 340901 | 224260 | 8 | 5 | 27 | 27 | Grosmont WwTW
River Wye/ Afon Gwy | GWENDDWR STW | Gwenddwr STW | AW1002201 | 7 | 20 | Powys | GWENDDWR BROOK | 306330 | 243400 | 8 | 8 | 27 | 27 | Gwenddwr STW
River Wye/ Afon Gwy | HUNDRED HOUSE STW | Hundred House STW | AW1002501 | 5.1 | 15.3 | Powys | COLWYN BROOK | 311040 | 254360 | 8 | 4 | 27 | 27 | Hundred House STW
River Wye/ Afon Gwy | LLANBADARN FFYNYDD STW , , | Llanbadarn Ffynydd STW | AW2005601 |  | 4 | Powys | ITHON RIVER | 309790 | 277730 | 8 | 8 | 27 | 27 | Llanbadarn Ffynydd STW
River Wye/ Afon Gwy | LLANBISTER STW LLANBISTER POWYS | Llanbister STW | AW1002601 | 14.61 |  | Powys | ITHON RIVER TRIBUTARY | 310810 | 273570 | 8 | 4 | 27 | 27 | Llanbister STW
River Wye/ Afon Gwy | LLANDEFALLE STW , , | Llandefalle STW | AW5001001 |  | 7.2 | Powys | TRIFFRWD BROOK | 312310 | 235140 | 8 | 8 | 27 | 27 | Llandefalle STW
River Wye/ Afon Gwy | LLANDEGLEY STW | Llandegley STW | AW1002701 | 13 | 39 | Powys | MITHIL BROOK | 313780 | 263110 | 5 | 1 | 27 | 27 | Llandegley STW
River Wye/ Afon Gwy | LLANDEWI RHYDDERCH STW MONMOUTHSHIE | Llandewi Rhydderch STW | AS1002101 | 30 |  | Monmouthshire | PANT BROOK | 335230 | 213080 | 5 | 8 | 27 | 27 | Llandewi Rhydderch STW
River Wye/ Afon Gwy | LLANDEWI YSTRADENNY STW | Llandewi Ystradenny STW | AW1002801 |  | 108 | Powys | ITHON RIVER | 310550 | 268170 | 8 | 8 | 27 | 27 | Llandewi Ystradenny STW
River Wye/ Afon Gwy | LLANDOGO STW SSO | Llandogo STW | AS1002201 | 182 | 1090 | Monmouthshire | WYE RIVER - TIDAL | 353020 | 204080 | 8 | 8 | 27 | 27 | Llandogo STW
River Wye/ Afon Gwy | LLANDRINDOD WELLS STW PARK LANE | Llandrindod Wells STW | AW1002901 | 1790 |  | Powys | RIVER ITHON | 304907 | 260500 | 0.8 | 0.8 | 27 | 27 | Llandrindod Wells STW
River Wye/ Afon Gwy | LLANFAREDD STW | Llanfaredd STW | AW1003001 | 6 |  | Powys | WYE RIVER | 306850 | 250450 | 8 | 8 | 27 | 27 | Llanfaredd STW
River Wye/ Afon Gwy | LLANFILO STW | Llanfilo STW | AW1003201 | 13 | 40 | Powys | DULAS BROOK | 311720 | 233900 | 8 | 2 | 27 | 27 | Llanfilo STW
River Wye/ Afon Gwy | Llangammarch Wells Wastewater Treatment Works | Llangammarch Wells WwTW | AW1003301 | 43 |  | Powys | River Irfon | 293679 | 247308 | 5 | 5 | 27 | 27 | Llangammarch Wells WwTW
River Wye/ Afon Gwy | LLANGUNLLO STW PS | Llangunllo STW | AW1003501 | 21 | 63 | Powys | RIVER LUGG | 321450 | 270830 | 8 | 8 | 27 | 27 | Llangunllo STW
River Wye/ Afon Gwy | LLANGURIG STW | Llangurig STW | AW1003601 | 36 | 108 | Powys | WYE RIVER | 290900 | 279600 | 5 | 5 | 27 | 27 | Llangurig STW
River Wye/ Afon Gwy | LLANIGON Wastewater Treatment Works | Llanigon WwTW | AW1003701 | 32.3 |  | Powys | DIGEDI BROOK | 320468 | 240493 | 5 | 5 | 27 | 27 | Llanigon WwTW
River Wye/ Afon Gwy | LLANTILIO CROSENNY STW ABERGAVENNY | Llantilio Crosenny STW | AS1002301 |  |  | Monmouthshire | TROTHY RIVER | 339730 | 214550 | 8 | 8 | 27 | 27 | Llantilio Crosenny STW
River Wye/ Afon Gwy | LLANVAPLEY STW | Llanvapley STW | AS1002601 |  |  | Monmouthshire | LLANYMYNACH BROOK | 336051 | 213949 | 8 | 8 | 27 | 27 | Llanvapley STW
River Wye/ Afon Gwy | LLANWRTHWL STW | Llanwrthwl STW | AW1003801 | 12 | 72 | Powys | RIVER WYE | 297760 | 263350 | 8 | 8 | 27 | 27 | Llanwrthwl STW
River Wye/ Afon Gwy | LLANWRTYD WELLS STW LLANWRTYD WELLS | Llanwrtyd Wells STW | AW1003901 | 382.1 |  | Powys | IRFON RIVER | 290030 | 246320 | 5 | 2 | 27 | 27 | Llanwrtyd Wells STW
River Wye/ Afon Gwy | Llanyre Wastewater Treatment Works | Llanyre WwTW | AW1004001 | 80 |  | Powys | RIVER ITHON | 305260 | 262340 | 5 | 5 | 27 | 27 | Llanyre WwTW
River Wye/ Afon Gwy | LLOWES STW | Llowes STW | AW1004101 | 16.4 | 98 | Powys | UN-NAMED TRIBUTARY OF RIVER WY | 319400 | 241600 | 8 | 8 | 27 | 27 | Llowes STW
River Wye/ Afon Gwy | LLYSWEN STW CHURCH ROAD LLYSWEN | Llyswen STW | AW1004201 | 132 |  | Powys | RIVER WYE | 313369 | 238152 | 5 | 5 | 27 | 27 | Llyswen STW
River Wye/ Afon Gwy | MONMOUTH STW REDBROOK ROAD MONMOUTH | Monmouth STW | AS1003201 | 2845 | 7250 | Monmouthshire | RIVER WYE | 351532 | 211795 | 2 | 2 | 27 | 27 | Monmouth STW
River Wye/ Afon Gwy | NARTH WASTEWATER TREATMENT WORKS | Narth WwTW | BP3227GK | 4.7 |  | Monmouthshire | Groundwater via infiltration system | 352260 | 206774 | 8 | 8 | 27 | 27 | Narth WwTW
River Wye/ Afon Gwy | NEW RADNOR STW SCHOOL LANE NEW RADN | New Radnor STW | AW1004501 | 141 | 851 | Powys | SUMMERGILL BROOK | 321807 | 260754 | 5 | 8 | 27 | 27 | New Radnor STW
River Wye/ Afon Gwy | NEWBRIDGE-ON-WYE STW POWYS | Newbridge-On-Wye STW | AW1004401 | 280 |  | Powys | RIVER WYE | 301470 | 258120 | 5 | 5 | 27 | 27 | Newbridge-On-Wye STW
River Wye/ Afon Gwy | OLD RADNOR STW | Old Radnor STW | AN0133901 | 10 | 30 | Powys | TRIB OF SUMMERGILL BROOK | 324640 | 259400 | 8 | 8 | 27 | 27 | Old Radnor STW
River Wye/ Afon Gwy | Package treatment plant (PTP) default | Package treatment plant (PTP) default | [7 empty] | 9.7 | 9.7 | 72.9 | 72.9 | Offer trin pecyn (PTP) rhagosodedig
River Wye/ Afon Gwy | Package treatment plant (PTP) user defined | Package treatment plant (PTP) user defined | [11 empty] | Defnyddiwr offer trin pecyn (PTP) wedi'i ddiffinio
River Wye/ Afon Gwy | PAINSCASTLE STW | Painscastle STW | AW1004901 | 14 |  | Powys | BACH HOWEY | 317100 | 246300 | 8 | 3.5 | 27 | 27 | Painscastle STW
River Wye/ Afon Gwy | PANDY STW PANDY MONMOUTHSHIRE | Pandy STW | AH1002901 | 176 | 464 | Monmouthshire | AFON HONDDU | 333518 | 222842 | 5 | 5 | 27 | 27 | Pandy STW
River Wye/ Afon Gwy | PANTYDWR STW | Pantydwr STW | AW1005001 | 15 | 45 | Powys | NANT TAWELAN | 298400 | 274600 | 8 | 8 | 27 | 27 | Pantydwr STW
River Wye/ Afon Gwy | PENRHOS STW PENRHOS RAGLAN | Penrhos STW | AS1003401 |  | 4.54 | Monmouthshire | TRIB OF NANT WECHAN | 341500 | 211540 | 8 | 8 | 27 | 27 | Penrhos STW
River Wye/ Afon Gwy | PENYBONT STW NR.LLANDRINDOD WELLS | Penybont STW | AN0115601 |  |  | Powys | ITHON | 311690 | 263880 | 5 | 5 | 27 | 27 | Penybont STW
River Wye/ Afon Gwy | PRESTEIGNE STW CLATTERBROOM | Presteigne STW | AW1005101 | 1140 |  | Powys | RIVER LUGG | 332232 | 264365 | 1 | 8 | 27 | 27 | Presteigne STW
River Wye/ Afon Gwy | RHAYADER STW RHAYADER | Rhayader STW | AW1005201 | 857 | 2571 | Powys | WYE RIVER | 297830 | 267290 | 3 | 3 | 27 | 27 | Rhayader STW
River Wye/ Afon Gwy | ROCKFIELD STW | Rockfield STW | AS1003601 |  | 55 | Monmouthshire | MONNOW RIVER | 348550 | 214780 | 8 | 8 | 27 | 27 | Rockfield STW
River Wye/ Afon Gwy | Septic tank default | Septic tank default | [7 empty] | 11.6 | 11.6 | 96.3 | 96.3 | Tanc septig rhagosodedig
River Wye/ Afon Gwy | Septic tank user defined | Septic tank user defined | [11 empty] | Defnyddiwr tanc septig wedi'i ddiffinio
River Wye/ Afon Gwy | TALGARTH STW BRONLLYS ROAD TALGARTH | Talgarth STW | AW1005301 | 841 |  | Powys | LLYNFI RIVER | 315073 | 234806 | 2 | 0.25 | 27 | 27 | Talgarth STW
River Wye/ Afon Gwy | TINTERN STW | Tintern STW | AS1004901 | 237.5 |  | Monmouthshire | WYE RIVER - TIDAL | 353500 | 200430 | 8 | 8 | 27 | 27 | Tintern STW
River Wye/ Afon Gwy | TIRABAD STW TIRABAD LLANGAMMARCH | Tirabad STW | AW2000201 | 12 |  | Powys | RIVER DULAS | 287920 | 241480 | 8 | 4 | 27 | 27 | Tirabad STW
River Wye/ Afon Gwy | VELINDRE STW | Velindre STW | AW1001701 | 11 | 33 | Powys | FELINDRE BROOK | 318350 | 236750 | 5 | 5 | 27 | 27 | Velindre STW
River Wye/ Afon Gwy | WWTW AT BROADSTONE (CATBROOK) | Broadstone (Catbrook) WwTW | BP3226XQ | 8.19 |  | Monmouthshire | A TRIB OF ANGHIDI FAWR | 350233 | 202772 | 8 | 8 | 27 | 27 | Broadstone (Catbrook) WwTW
Table 4: Stage 2 and 3 soil drainage lookup
Soilscape drainage term | Translation | Farmscoper term | Definition
Freely draining | Yn draenio'n rhydd (Freely draining) | FreeDrain | Free Draining
Slightly impeded drainage | Rhwystro ychydig ar ddraenio (Slightly impeded drainage) | DrainedAr | Drained for arable
Impeded drainage | Rhwystro draenio (Impeded drainage) | DrainedArGr | Drained for arable and grassland
Variable | Amrywiol (Variable) | DrainedAr | Drained for arable
Surface Wetness | Gwlypder Arwyneb (Surface Wetness) | DrainedAr | Drained for arable
Naturally wet | Yn naturiol wlyb (Naturally wet) | DrainedAr | Drained for arable
Table 5: Stage 2 and 3 landcover phosphorus export coefficient lookup
SAC | Landcover | Translation | Climate | Farmscoper Soil Drainage Term | Lookup | Phosphorous export coefficient | Nitrogen export coefficient
Afon Eden - Cors Goch Trawsfynydd | Cereals | Grawnfwydydd | 1200to1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddCereals1200to1500FreeDrain | 0.16 | 7.13
Afon Eden - Cors Goch Trawsfynydd | Cereals | Grawnfwydydd | 1200to1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddCereals1200to1500DrainedAr | 0.22 | 7.65
Afon Eden - Cors Goch Trawsfynydd | Cereals | Grawnfwydydd | 1200to1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddCereals1200to1500DrainedArGr | 0.96 | 7.51
Afon Eden - Cors Goch Trawsfynydd | Cereals | Grawnfwydydd | Over1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddCerealsOver1500FreeDrain | 0.26 | 6.76
Afon Eden - Cors Goch Trawsfynydd | Cereals | Grawnfwydydd | Over1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddCerealsOver1500DrainedAr | 0.3 | 8.45
Afon Eden - Cors Goch Trawsfynydd | Cereals | Grawnfwydydd | Over1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddCerealsOver1500DrainedArGr | 1.47 | 9.57
Afon Eden - Cors Goch Trawsfynydd | General cropping | Cnydio cyffredinol | 1200to1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddGeneral cropping1200to1500FreeDrain | 0.17 | 4.71
Afon Eden - Cors Goch Trawsfynydd | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddGeneral cropping1200to1500DrainedAr | 0.22 | 5.04
Afon Eden - Cors Goch Trawsfynydd | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddGeneral cropping1200to1500DrainedArGr | 0.99 | 4.92
Afon Eden - Cors Goch Trawsfynydd | General cropping | Cnydio cyffredinol | Over1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddGeneral croppingOver1500FreeDrain | 0.27 | 4.5
Afon Eden - Cors Goch Trawsfynydd | General cropping | Cnydio cyffredinol | Over1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddGeneral croppingOver1500DrainedAr | 0.31 | 5.65
Afon Eden - Cors Goch Trawsfynydd | General cropping | Cnydio cyffredinol | Over1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddGeneral croppingOver1500DrainedArGr | 1.56 | 6.85
Afon Eden - Cors Goch Trawsfynydd | Horticulture | Garddwriaeth | 1200to1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddHorticulture1200to1500FreeDrain | 0.16 | 5.36
Afon Eden - Cors Goch Trawsfynydd | Horticulture | Garddwriaeth | 1200to1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddHorticulture1200to1500DrainedAr | 0.26 | 5.63
Afon Eden - Cors Goch Trawsfynydd | Horticulture | Garddwriaeth | 1200to1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddHorticulture1200to1500DrainedArGr | 0.92 | 5.37
Afon Eden - Cors Goch Trawsfynydd | Horticulture | Garddwriaeth | Over1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddHorticultureOver1500FreeDrain | 0.27 | 5.22
Afon Eden - Cors Goch Trawsfynydd | Horticulture | Garddwriaeth | Over1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddHorticultureOver1500DrainedAr | 0.37 | 6.33
Afon Eden - Cors Goch Trawsfynydd | Horticulture | Garddwriaeth | Over1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddHorticultureOver1500DrainedArGr | 1.49 | 7.19
Afon Eden - Cors Goch Trawsfynydd | Indoor pig farming | Ffermio moch dan do | 1200to1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddIndoor pig farming1200to1500FreeDrain | 0.41 | 36.77
Afon Eden - Cors Goch Trawsfynydd | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddIndoor pig farming1200to1500DrainedAr | 1.56 | 36.02
Afon Eden - Cors Goch Trawsfynydd | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddIndoor pig farming1200to1500DrainedArGr | 2.14 | 26.2
Afon Eden - Cors Goch Trawsfynydd | Indoor pig farming | Ffermio moch dan do | Over1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddIndoor pig farmingOver1500FreeDrain | 0.75 | 37.82
Afon Eden - Cors Goch Trawsfynydd | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddIndoor pig farmingOver1500DrainedAr | 2.11 | 42.18
Afon Eden - Cors Goch Trawsfynydd | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddIndoor pig farmingOver1500DrainedArGr | 3.77 | 31.5
Afon Eden - Cors Goch Trawsfynydd | Poultry | Dofednod | 1200to1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddPoultry1200to1500FreeDrain | 0.38 | 23.15
Afon Eden - Cors Goch Trawsfynydd | Poultry | Dofednod | 1200to1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddPoultry1200to1500DrainedAr | 1.49 | 23.03
Afon Eden - Cors Goch Trawsfynydd | Poultry | Dofednod | 1200to1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddPoultry1200to1500DrainedArGr | 1.8 | 17.88
Afon Eden - Cors Goch Trawsfynydd | Poultry | Dofednod | Over1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddPoultryOver1500FreeDrain | 0.71 | 23.76
Afon Eden - Cors Goch Trawsfynydd | Poultry | Dofednod | Over1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddPoultryOver1500DrainedAr | 2.04 | 27.06
Afon Eden - Cors Goch Trawsfynydd | Poultry | Dofednod | Over1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddPoultryOver1500DrainedArGr | 3.38 | 21.93
Afon Eden - Cors Goch Trawsfynydd | Dairy | Llaeth | 1200to1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddDairy1200to1500FreeDrain | 0.2 | 6.63
Afon Eden - Cors Goch Trawsfynydd | Dairy | Llaeth | 1200to1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddDairy1200to1500DrainedAr | 0.24 | 7.5
Afon Eden - Cors Goch Trawsfynydd | Dairy | Llaeth | 1200to1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddDairy1200to1500DrainedArGr | 1.17 | 11.02
Afon Eden - Cors Goch Trawsfynydd | Dairy | Llaeth | Over1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddDairyOver1500FreeDrain | 0.31 | 6.54
Afon Eden - Cors Goch Trawsfynydd | Dairy | Llaeth | Over1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddDairyOver1500DrainedAr | 0.33 | 8.39
Afon Eden - Cors Goch Trawsfynydd | Dairy | Llaeth | Over1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddDairyOver1500DrainedArGr | 1.8 | 15.9
Afon Eden - Cors Goch Trawsfynydd | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddLess Favoured Area grazing1200to1500FreeDrain | 0.19 | 7.85
Afon Eden - Cors Goch Trawsfynydd | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddLess Favoured Area grazing1200to1500DrainedAr | 0.21 | 8.28
Afon Eden - Cors Goch Trawsfynydd | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddLess Favoured Area grazing1200to1500DrainedArGr | 0.6 | 8.19
Afon Eden - Cors Goch Trawsfynydd | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddLess Favoured Area grazingOver1500FreeDrain | 0.32 | 7.65
Afon Eden - Cors Goch Trawsfynydd | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddLess Favoured Area grazingOver1500DrainedAr | 0.3 | 8.64
Afon Eden - Cors Goch Trawsfynydd | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddLess Favoured Area grazingOver1500DrainedArGr | 0.92 | 9.33
Afon Eden - Cors Goch Trawsfynydd | Lowland grazing | Pori iseldir | 1200to1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddLowland grazing1200to1500FreeDrain | 0.23 | 11.39
Afon Eden - Cors Goch Trawsfynydd | Lowland grazing | Pori iseldir | 1200to1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddLowland grazing1200to1500DrainedAr | 0.29 | 12.43
Afon Eden - Cors Goch Trawsfynydd | Lowland grazing | Pori iseldir | 1200to1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddLowland grazing1200to1500DrainedArGr | 1.3 | 12.49
Afon Eden - Cors Goch Trawsfynydd | Lowland grazing | Pori iseldir | Over1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddLowland grazingOver1500FreeDrain | 0.37 | 10.72
Afon Eden - Cors Goch Trawsfynydd | Lowland grazing | Pori iseldir | Over1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddLowland grazingOver1500DrainedAr | 0.39 | 13.45
Afon Eden - Cors Goch Trawsfynydd | Lowland grazing | Pori iseldir | Over1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddLowland grazingOver1500DrainedArGr | 1.9 | 15.33
Afon Eden - Cors Goch Trawsfynydd | Mixed | Cymysg | 1200to1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddMixed1200to1500FreeDrain | 0.22 | 11.53
Afon Eden - Cors Goch Trawsfynydd | Mixed | Cymysg | 1200to1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddMixed1200to1500DrainedAr | 0.29 | 12.6
Afon Eden - Cors Goch Trawsfynydd | Mixed | Cymysg | 1200to1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddMixed1200to1500DrainedArGr | 1.31 | 12.99
Afon Eden - Cors Goch Trawsfynydd | Mixed | Cymysg | Over1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddMixedOver1500FreeDrain | 0.35 | 10.86
Afon Eden - Cors Goch Trawsfynydd | Mixed | Cymysg | Over1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddMixedOver1500DrainedAr | 0.37 | 13.64
Afon Eden - Cors Goch Trawsfynydd | Mixed | Cymysg | Over1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddMixedOver1500DrainedArGr | 1.92 | 16.12
Afon Eden - Cors Goch Trawsfynydd | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddOutdoor pig farming1200to1500FreeDrain | 0.84 | 9.96
Afon Eden - Cors Goch Trawsfynydd | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddOutdoor pig farming1200to1500DrainedAr | 4.79 | 8.89
Afon Eden - Cors Goch Trawsfynydd | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddOutdoor pig farming1200to1500DrainedArGr | 4.44 | 4.94
Afon Eden - Cors Goch Trawsfynydd | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | FreeDrain | Afon Eden - Cors Goch TrawsfynyddOutdoor pig farmingOver1500FreeDrain | 1.64 | 9.96
Afon Eden - Cors Goch Trawsfynydd | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedAr | Afon Eden - Cors Goch TrawsfynyddOutdoor pig farmingOver1500DrainedAr | 6.12 | 9.69
Afon Eden - Cors Goch Trawsfynydd | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedArGr | Afon Eden - Cors Goch TrawsfynyddOutdoor pig farmingOver1500DrainedArGr | 8.63 | 4.93
Afon Gwyrfai a Llyn Cwellyn | Cereals | Grawnfwydydd | 900to1200 | FreeDrain | Afon Gwyrfai a Llyn CwellynCereals900to1200FreeDrain | 0.11 | 6.07
Afon Gwyrfai a Llyn Cwellyn | Cereals | Grawnfwydydd | 900to1200 | DrainedAr | Afon Gwyrfai a Llyn CwellynCereals900to1200DrainedAr | 0.14 | 5.72
Afon Gwyrfai a Llyn Cwellyn | Cereals | Grawnfwydydd | 900to1200 | DrainedArGr | Afon Gwyrfai a Llyn CwellynCereals900to1200DrainedArGr | 0.61 | 4.72
Afon Gwyrfai a Llyn Cwellyn | Cereals | Grawnfwydydd | 1200to1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynCereals1200to1500FreeDrain | 0.16 | 6.64
Afon Gwyrfai a Llyn Cwellyn | Cereals | Grawnfwydydd | 1200to1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynCereals1200to1500DrainedAr | 0.22 | 7.08
Afon Gwyrfai a Llyn Cwellyn | Cereals | Grawnfwydydd | 1200to1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynCereals1200to1500DrainedArGr | 0.94 | 6.75
Afon Gwyrfai a Llyn Cwellyn | Cereals | Grawnfwydydd | Over1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynCerealsOver1500FreeDrain | 0.26 | 6.3
Afon Gwyrfai a Llyn Cwellyn | Cereals | Grawnfwydydd | Over1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynCerealsOver1500DrainedAr | 0.31 | 7.84
Afon Gwyrfai a Llyn Cwellyn | Cereals | Grawnfwydydd | Over1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynCerealsOver1500DrainedArGr | 1.46 | 8.71
Afon Gwyrfai a Llyn Cwellyn | General cropping | Cnydio cyffredinol | 900to1200 | FreeDrain | Afon Gwyrfai a Llyn CwellynGeneral cropping900to1200FreeDrain | 0.12 | 4.68
Afon Gwyrfai a Llyn Cwellyn | General cropping | Cnydio cyffredinol | 900to1200 | DrainedAr | Afon Gwyrfai a Llyn CwellynGeneral cropping900to1200DrainedAr | 0.17 | 4.33
Afon Gwyrfai a Llyn Cwellyn | General cropping | Cnydio cyffredinol | 900to1200 | DrainedArGr | Afon Gwyrfai a Llyn CwellynGeneral cropping900to1200DrainedArGr | 0.66 | 3.53
Afon Gwyrfai a Llyn Cwellyn | General cropping | Cnydio cyffredinol | 1200to1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynGeneral cropping1200to1500FreeDrain | 0.18 | 5.03
Afon Gwyrfai a Llyn Cwellyn | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynGeneral cropping1200to1500DrainedAr | 0.28 | 5.34
Afon Gwyrfai a Llyn Cwellyn | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynGeneral cropping1200to1500DrainedArGr | 1.03 | 5.16
Afon Gwyrfai a Llyn Cwellyn | General cropping | Cnydio cyffredinol | Over1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynGeneral croppingOver1500FreeDrain | 0.29 | 4.83
Afon Gwyrfai a Llyn Cwellyn | General cropping | Cnydio cyffredinol | Over1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynGeneral croppingOver1500DrainedAr | 0.38 | 6
Afon Gwyrfai a Llyn Cwellyn | General cropping | Cnydio cyffredinol | Over1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynGeneral croppingOver1500DrainedArGr | 1.66 | 7.14
Afon Gwyrfai a Llyn Cwellyn | Horticulture | Garddwriaeth | 900to1200 | FreeDrain | Afon Gwyrfai a Llyn CwellynHorticulture900to1200FreeDrain | 0.12 | 5.61
Afon Gwyrfai a Llyn Cwellyn | Horticulture | Garddwriaeth | 900to1200 | DrainedAr | Afon Gwyrfai a Llyn CwellynHorticulture900to1200DrainedAr | 0.24 | 5.05
Afon Gwyrfai a Llyn Cwellyn | Horticulture | Garddwriaeth | 900to1200 | DrainedArGr | Afon Gwyrfai a Llyn CwellynHorticulture900to1200DrainedArGr | 0.67 | 4.12
Afon Gwyrfai a Llyn Cwellyn | Horticulture | Garddwriaeth | 1200to1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynHorticulture1200to1500FreeDrain | 0.19 | 6.15
Afon Gwyrfai a Llyn Cwellyn | Horticulture | Garddwriaeth | 1200to1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynHorticulture1200to1500DrainedAr | 0.4 | 6.35
Afon Gwyrfai a Llyn Cwellyn | Horticulture | Garddwriaeth | 1200to1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynHorticulture1200to1500DrainedArGr | 1.03 | 5.87
Afon Gwyrfai a Llyn Cwellyn | Horticulture | Garddwriaeth | Over1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynHorticultureOver1500FreeDrain | 0.32 | 6.03
Afon Gwyrfai a Llyn Cwellyn | Horticulture | Garddwriaeth | Over1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynHorticultureOver1500DrainedAr | 0.54 | 7.19
Afon Gwyrfai a Llyn Cwellyn | Horticulture | Garddwriaeth | Over1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynHorticultureOver1500DrainedArGr | 1.71 | 7.79
Afon Gwyrfai a Llyn Cwellyn | Indoor pig farming | Ffermio moch dan do | 900to1200 | FreeDrain | Afon Gwyrfai a Llyn CwellynIndoor pig farming900to1200FreeDrain | 0.22 | 23.22
Afon Gwyrfai a Llyn Cwellyn | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedAr | Afon Gwyrfai a Llyn CwellynIndoor pig farming900to1200DrainedAr | 0.67 | 20.15
Afon Gwyrfai a Llyn Cwellyn | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedArGr | Afon Gwyrfai a Llyn CwellynIndoor pig farming900to1200DrainedArGr | 1.29 | 14.86
Afon Gwyrfai a Llyn Cwellyn | Indoor pig farming | Ffermio moch dan do | 1200to1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynIndoor pig farming1200to1500FreeDrain | 0.33 | 24.15
Afon Gwyrfai a Llyn Cwellyn | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynIndoor pig farming1200to1500DrainedAr | 1.08 | 23.87
Afon Gwyrfai a Llyn Cwellyn | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynIndoor pig farming1200to1500DrainedArGr | 1.82 | 17.93
Afon Gwyrfai a Llyn Cwellyn | Indoor pig farming | Ffermio moch dan do | Over1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynIndoor pig farmingOver1500FreeDrain | 0.58 | 24.47
Afon Gwyrfai a Llyn Cwellyn | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynIndoor pig farmingOver1500DrainedAr | 1.45 | 27.81
Afon Gwyrfai a Llyn Cwellyn | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynIndoor pig farmingOver1500DrainedArGr | 3.07 | 22
Afon Gwyrfai a Llyn Cwellyn | Poultry | Dofednod | 900to1200 | FreeDrain | Afon Gwyrfai a Llyn CwellynPoultry900to1200FreeDrain | 0.2 | 16.32
Afon Gwyrfai a Llyn Cwellyn | Poultry | Dofednod | 900to1200 | DrainedAr | Afon Gwyrfai a Llyn CwellynPoultry900to1200DrainedAr | 0.64 | 13.82
Afon Gwyrfai a Llyn Cwellyn | Poultry | Dofednod | 900to1200 | DrainedArGr | Afon Gwyrfai a Llyn CwellynPoultry900to1200DrainedArGr | 1.03 | 11.03
Afon Gwyrfai a Llyn Cwellyn | Poultry | Dofednod | 1200to1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynPoultry1200to1500FreeDrain | 0.3 | 17.04
Afon Gwyrfai a Llyn Cwellyn | Poultry | Dofednod | 1200to1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynPoultry1200to1500DrainedAr | 1.04 | 16.67
Afon Gwyrfai a Llyn Cwellyn | Poultry | Dofednod | 1200to1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynPoultry1200to1500DrainedArGr | 1.53 | 13.52
Afon Gwyrfai a Llyn Cwellyn | Poultry | Dofednod | Over1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynPoultryOver1500FreeDrain | 0.55 | 17.35
Afon Gwyrfai a Llyn Cwellyn | Poultry | Dofednod | Over1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynPoultryOver1500DrainedAr | 1.41 | 19.27
Afon Gwyrfai a Llyn Cwellyn | Poultry | Dofednod | Over1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynPoultryOver1500DrainedArGr | 2.73 | 16.75
Afon Gwyrfai a Llyn Cwellyn | Dairy | Llaeth | 900to1200 | FreeDrain | Afon Gwyrfai a Llyn CwellynDairy900to1200FreeDrain | 0.17 | 14.39
Afon Gwyrfai a Llyn Cwellyn | Dairy | Llaeth | 900to1200 | DrainedAr | Afon Gwyrfai a Llyn CwellynDairy900to1200DrainedAr | 0.19 | 13.66
Afon Gwyrfai a Llyn Cwellyn | Dairy | Llaeth | 900to1200 | DrainedArGr | Afon Gwyrfai a Llyn CwellynDairy900to1200DrainedArGr | 1.01 | 11.88
Afon Gwyrfai a Llyn Cwellyn | Dairy | Llaeth | 1200to1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynDairy1200to1500FreeDrain | 0.24 | 14.19
Afon Gwyrfai a Llyn Cwellyn | Dairy | Llaeth | 1200to1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynDairy1200to1500DrainedAr | 0.29 | 15.52
Afon Gwyrfai a Llyn Cwellyn | Dairy | Llaeth | 1200to1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynDairy1200to1500DrainedArGr | 1.5 | 15.93
Afon Gwyrfai a Llyn Cwellyn | Dairy | Llaeth | Over1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynDairyOver1500FreeDrain | 0.36 | 13.33
Afon Gwyrfai a Llyn Cwellyn | Dairy | Llaeth | Over1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynDairyOver1500DrainedAr | 0.38 | 17.51
Afon Gwyrfai a Llyn Cwellyn | Dairy | Llaeth | Over1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynDairyOver1500DrainedArGr | 2.22 | 22.17
Afon Gwyrfai a Llyn Cwellyn | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | FreeDrain | Afon Gwyrfai a Llyn CwellynLess Favoured Area grazing900to1200FreeDrain | 0.13 | 7.85
Afon Gwyrfai a Llyn Cwellyn | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedAr | Afon Gwyrfai a Llyn CwellynLess Favoured Area grazing900to1200DrainedAr | 0.13 | 7.63
Afon Gwyrfai a Llyn Cwellyn | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedArGr | Afon Gwyrfai a Llyn CwellynLess Favoured Area grazing900to1200DrainedArGr | 0.51 | 6.96
Afon Gwyrfai a Llyn Cwellyn | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynLess Favoured Area grazing1200to1500FreeDrain | 0.2 | 7.77
Afon Gwyrfai a Llyn Cwellyn | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynLess Favoured Area grazing1200to1500DrainedAr | 0.22 | 8.26
Afon Gwyrfai a Llyn Cwellyn | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynLess Favoured Area grazing1200to1500DrainedArGr | 0.76 | 8.03
Afon Gwyrfai a Llyn Cwellyn | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynLess Favoured Area grazingOver1500FreeDrain | 0.32 | 7.45
Afon Gwyrfai a Llyn Cwellyn | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynLess Favoured Area grazingOver1500DrainedAr | 0.31 | 8.77
Afon Gwyrfai a Llyn Cwellyn | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynLess Favoured Area grazingOver1500DrainedArGr | 1.16 | 9.49
Afon Gwyrfai a Llyn Cwellyn | Lowland grazing | Pori iseldir | 900to1200 | FreeDrain | Afon Gwyrfai a Llyn CwellynLowland grazing900to1200FreeDrain | 0.17 | 11.6
Afon Gwyrfai a Llyn Cwellyn | Lowland grazing | Pori iseldir | 900to1200 | DrainedAr | Afon Gwyrfai a Llyn CwellynLowland grazing900to1200DrainedAr | 0.19 | 11.07
Afon Gwyrfai a Llyn Cwellyn | Lowland grazing | Pori iseldir | 900to1200 | DrainedArGr | Afon Gwyrfai a Llyn CwellynLowland grazing900to1200DrainedArGr | 0.94 | 9.44
Afon Gwyrfai a Llyn Cwellyn | Lowland grazing | Pori iseldir | 1200to1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynLowland grazing1200to1500FreeDrain | 0.23 | 11.43
Afon Gwyrfai a Llyn Cwellyn | Lowland grazing | Pori iseldir | 1200to1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynLowland grazing1200to1500DrainedAr | 0.3 | 12.43
Afon Gwyrfai a Llyn Cwellyn | Lowland grazing | Pori iseldir | 1200to1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynLowland grazing1200to1500DrainedArGr | 1.38 | 11.76
Afon Gwyrfai a Llyn Cwellyn | Lowland grazing | Pori iseldir | Over1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynLowland grazingOver1500FreeDrain | 0.36 | 10.65
Afon Gwyrfai a Llyn Cwellyn | Lowland grazing | Pori iseldir | Over1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynLowland grazingOver1500DrainedAr | 0.4 | 13.65
Afon Gwyrfai a Llyn Cwellyn | Lowland grazing | Pori iseldir | Over1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynLowland grazingOver1500DrainedArGr | 2.05 | 14.77
Afon Gwyrfai a Llyn Cwellyn | Mixed | Cymysg | 900to1200 | FreeDrain | Afon Gwyrfai a Llyn CwellynMixed900to1200FreeDrain | 0.16 | 12.17
Afon Gwyrfai a Llyn Cwellyn | Mixed | Cymysg | 900to1200 | DrainedAr | Afon Gwyrfai a Llyn CwellynMixed900to1200DrainedAr | 0.18 | 11.61
Afon Gwyrfai a Llyn Cwellyn | Mixed | Cymysg | 900to1200 | DrainedArGr | Afon Gwyrfai a Llyn CwellynMixed900to1200DrainedArGr | 0.97 | 10.07
Afon Gwyrfai a Llyn Cwellyn | Mixed | Cymysg | 1200to1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynMixed1200to1500FreeDrain | 0.22 | 12.05
Afon Gwyrfai a Llyn Cwellyn | Mixed | Cymysg | 1200to1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynMixed1200to1500DrainedAr | 0.29 | 13.13
Afon Gwyrfai a Llyn Cwellyn | Mixed | Cymysg | 1200to1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynMixed1200to1500DrainedArGr | 1.42 | 12.75
Afon Gwyrfai a Llyn Cwellyn | Mixed | Cymysg | Over1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynMixedOver1500FreeDrain | 0.35 | 11.2
Afon Gwyrfai a Llyn Cwellyn | Mixed | Cymysg | Over1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynMixedOver1500DrainedAr | 0.38 | 14.41
Afon Gwyrfai a Llyn Cwellyn | Mixed | Cymysg | Over1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynMixedOver1500DrainedArGr | 2.08 | 16.2
Afon Gwyrfai a Llyn Cwellyn | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | FreeDrain | Afon Gwyrfai a Llyn CwellynOutdoor pig farming900to1200FreeDrain | 0.54 | 9.96
Afon Gwyrfai a Llyn Cwellyn | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedAr | Afon Gwyrfai a Llyn CwellynOutdoor pig farming900to1200DrainedAr | 3.04 | 8.49
Afon Gwyrfai a Llyn Cwellyn | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedArGr | Afon Gwyrfai a Llyn CwellynOutdoor pig farming900to1200DrainedArGr | 3.32 | 4.99
Afon Gwyrfai a Llyn Cwellyn | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynOutdoor pig farming1200to1500FreeDrain | 0.84 | 9.96
Afon Gwyrfai a Llyn Cwellyn | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynOutdoor pig farming1200to1500DrainedAr | 4.79 | 8.89
Afon Gwyrfai a Llyn Cwellyn | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynOutdoor pig farming1200to1500DrainedArGr | 4.44 | 4.94
Afon Gwyrfai a Llyn Cwellyn | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | FreeDrain | Afon Gwyrfai a Llyn CwellynOutdoor pig farmingOver1500FreeDrain | 1.64 | 9.96
Afon Gwyrfai a Llyn Cwellyn | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedAr | Afon Gwyrfai a Llyn CwellynOutdoor pig farmingOver1500DrainedAr | 6.12 | 9.69
Afon Gwyrfai a Llyn Cwellyn | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedArGr | Afon Gwyrfai a Llyn CwellynOutdoor pig farmingOver1500DrainedArGr | 8.63 | 4.93
Afon Teifi/ River Teifi | Cereals | Grawnfwydydd | 700to900 | FreeDrain | Afon Teifi/ River TeifiCereals700to900FreeDrain | 0.09 | 9.88
Afon Teifi/ River Teifi | Cereals | Grawnfwydydd | 700to900 | DrainedAr | Afon Teifi/ River TeifiCereals700to900DrainedAr | 0.22 | 7.98
Afon Teifi/ River Teifi | Cereals | Grawnfwydydd | 700to900 | DrainedArGr | Afon Teifi/ River TeifiCereals700to900DrainedArGr | 0.48 | 6.96
Afon Teifi/ River Teifi | Cereals | Grawnfwydydd | 900to1200 | FreeDrain | Afon Teifi/ River TeifiCereals900to1200FreeDrain | 0.15 | 11.05
Afon Teifi/ River Teifi | Cereals | Grawnfwydydd | 900to1200 | DrainedAr | Afon Teifi/ River TeifiCereals900to1200DrainedAr | 0.41 | 10.78
Afon Teifi/ River Teifi | Cereals | Grawnfwydydd | 900to1200 | DrainedArGr | Afon Teifi/ River TeifiCereals900to1200DrainedArGr | 0.84 | 9.2
Afon Teifi/ River Teifi | Cereals | Grawnfwydydd | 1200to1500 | FreeDrain | Afon Teifi/ River TeifiCereals1200to1500FreeDrain | 0.23 | 11.65
Afon Teifi/ River Teifi | Cereals | Grawnfwydydd | 1200to1500 | DrainedAr | Afon Teifi/ River TeifiCereals1200to1500DrainedAr | 0.66 | 13.3
Afon Teifi/ River Teifi | Cereals | Grawnfwydydd | 1200to1500 | DrainedArGr | Afon Teifi/ River TeifiCereals1200to1500DrainedArGr | 1.25 | 12.03
Afon Teifi/ River Teifi | Cereals | Grawnfwydydd | Over1500 | FreeDrain | Afon Teifi/ River TeifiCerealsOver1500FreeDrain | 0.39 | 11.73
Afon Teifi/ River Teifi | Cereals | Grawnfwydydd | Over1500 | DrainedAr | Afon Teifi/ River TeifiCerealsOver1500DrainedAr | 0.89 | 15.63
Afon Teifi/ River Teifi | Cereals | Grawnfwydydd | Over1500 | DrainedArGr | Afon Teifi/ River TeifiCerealsOver1500DrainedArGr | 2.14 | 15.56
Afon Teifi/ River Teifi | General cropping | Cnydio cyffredinol | 700to900 | FreeDrain | Afon Teifi/ River TeifiGeneral cropping700to900FreeDrain | 0.08 | 5.59
Afon Teifi/ River Teifi | General cropping | Cnydio cyffredinol | 700to900 | DrainedAr | Afon Teifi/ River TeifiGeneral cropping700to900DrainedAr | 0.14 | 4.36
Afon Teifi/ River Teifi | General cropping | Cnydio cyffredinol | 700to900 | DrainedArGr | Afon Teifi/ River TeifiGeneral cropping700to900DrainedArGr | 0.4 | 3.42
Afon Teifi/ River Teifi | General cropping | Cnydio cyffredinol | 900to1200 | FreeDrain | Afon Teifi/ River TeifiGeneral cropping900to1200FreeDrain | 0.13 | 6.27
Afon Teifi/ River Teifi | General cropping | Cnydio cyffredinol | 900to1200 | DrainedAr | Afon Teifi/ River TeifiGeneral cropping900to1200DrainedAr | 0.26 | 5.84
Afon Teifi/ River Teifi | General cropping | Cnydio cyffredinol | 900to1200 | DrainedArGr | Afon Teifi/ River TeifiGeneral cropping900to1200DrainedArGr | 0.74 | 4.89
Afon Teifi/ River Teifi | General cropping | Cnydio cyffredinol | 1200to1500 | FreeDrain | Afon Teifi/ River TeifiGeneral cropping1200to1500FreeDrain | 0.2 | 6.65
Afon Teifi/ River Teifi | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedAr | Afon Teifi/ River TeifiGeneral cropping1200to1500DrainedAr | 0.43 | 7.19
Afon Teifi/ River Teifi | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedArGr | Afon Teifi/ River TeifiGeneral cropping1200to1500DrainedArGr | 1.14 | 6.75
Afon Teifi/ River Teifi | General cropping | Cnydio cyffredinol | Over1500 | FreeDrain | Afon Teifi/ River TeifiGeneral croppingOver1500FreeDrain | 0.34 | 6.56
Afon Teifi/ River Teifi | General cropping | Cnydio cyffredinol | Over1500 | DrainedAr | Afon Teifi/ River TeifiGeneral croppingOver1500DrainedAr | 0.58 | 8.29
Afon Teifi/ River Teifi | General cropping | Cnydio cyffredinol | Over1500 | DrainedArGr | Afon Teifi/ River TeifiGeneral croppingOver1500DrainedArGr | 1.88 | 9.15
Afon Teifi/ River Teifi | Horticulture | Garddwriaeth | 700to900 | FreeDrain | Afon Teifi/ River TeifiHorticulture700to900FreeDrain | 0.08 | 6.52
Afon Teifi/ River Teifi | Horticulture | Garddwriaeth | 700to900 | DrainedAr | Afon Teifi/ River TeifiHorticulture700to900DrainedAr | 0.17 | 4.99
Afon Teifi/ River Teifi | Horticulture | Garddwriaeth | 700to900 | DrainedArGr | Afon Teifi/ River TeifiHorticulture700to900DrainedArGr | 0.42 | 4.08
Afon Teifi/ River Teifi | Horticulture | Garddwriaeth | 900to1200 | FreeDrain | Afon Teifi/ River TeifiHorticulture900to1200FreeDrain | 0.14 | 7.4
Afon Teifi/ River Teifi | Horticulture | Garddwriaeth | 900to1200 | DrainedAr | Afon Teifi/ River TeifiHorticulture900to1200DrainedAr | 0.33 | 6.74
Afon Teifi/ River Teifi | Horticulture | Garddwriaeth | 900to1200 | DrainedArGr | Afon Teifi/ River TeifiHorticulture900to1200DrainedArGr | 0.75 | 5.64
Afon Teifi/ River Teifi | Horticulture | Garddwriaeth | 1200to1500 | FreeDrain | Afon Teifi/ River TeifiHorticulture1200to1500FreeDrain | 0.21 | 7.95
Afon Teifi/ River Teifi | Horticulture | Garddwriaeth | 1200to1500 | DrainedAr | Afon Teifi/ River TeifiHorticulture1200to1500DrainedAr | 0.54 | 8.4
Afon Teifi/ River Teifi | Horticulture | Garddwriaeth | 1200to1500 | DrainedArGr | Afon Teifi/ River TeifiHorticulture1200to1500DrainedArGr | 1.15 | 7.64
Afon Teifi/ River Teifi | Horticulture | Garddwriaeth | Over1500 | FreeDrain | Afon Teifi/ River TeifiHorticultureOver1500FreeDrain | 0.37 | 7.96
Afon Teifi/ River Teifi | Horticulture | Garddwriaeth | Over1500 | DrainedAr | Afon Teifi/ River TeifiHorticultureOver1500DrainedAr | 0.74 | 9.71
Afon Teifi/ River Teifi | Horticulture | Garddwriaeth | Over1500 | DrainedArGr | Afon Teifi/ River TeifiHorticultureOver1500DrainedArGr | 1.95 | 10.06
Afon Teifi/ River Teifi | Indoor pig farming | Ffermio moch dan do | 700to900 | FreeDrain | Afon Teifi/ River TeifiIndoor pig farming700to900FreeDrain | 0.15 | 22.73
Afon Teifi/ River Teifi | Indoor pig farming | Ffermio moch dan do | 700to900 | DrainedAr | Afon Teifi/ River TeifiIndoor pig farming700to900DrainedAr | 0.56 | 17.33
Afon Teifi/ River Teifi | Indoor pig farming | Ffermio moch dan do | 700to900 | DrainedArGr | Afon Teifi/ River TeifiIndoor pig farming700to900DrainedArGr | 0.82 | 15.48
Afon Teifi/ River Teifi | Indoor pig farming | Ffermio moch dan do | 900to1200 | FreeDrain | Afon Teifi/ River TeifiIndoor pig farming900to1200FreeDrain | 0.28 | 24.43
Afon Teifi/ River Teifi | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedAr | Afon Teifi/ River TeifiIndoor pig farming900to1200DrainedAr | 1.08 | 22.02
Afon Teifi/ River Teifi | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedArGr | Afon Teifi/ River TeifiIndoor pig farming900to1200DrainedArGr | 1.37 | 18.03
Afon Teifi/ River Teifi | Indoor pig farming | Ffermio moch dan do | 1200to1500 | FreeDrain | Afon Teifi/ River TeifiIndoor pig farming1200to1500FreeDrain | 0.42 | 25.17
Afon Teifi/ River Teifi | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedAr | Afon Teifi/ River TeifiIndoor pig farming1200to1500DrainedAr | 1.76 | 26.72
Afon Teifi/ River Teifi | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedArGr | Afon Teifi/ River TeifiIndoor pig farming1200to1500DrainedArGr | 2 | 21.55
Afon Teifi/ River Teifi | Indoor pig farming | Ffermio moch dan do | Over1500 | FreeDrain | Afon Teifi/ River TeifiIndoor pig farmingOver1500FreeDrain | 0.77 | 26.12
Afon Teifi/ River Teifi | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedAr | Afon Teifi/ River TeifiIndoor pig farmingOver1500DrainedAr | 2.38 | 31.93
Afon Teifi/ River Teifi | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedArGr | Afon Teifi/ River TeifiIndoor pig farmingOver1500DrainedArGr | 3.78 | 26.98
Afon Teifi/ River Teifi | Poultry | Dofednod | 700to900 | FreeDrain | Afon Teifi/ River TeifiPoultry700to900FreeDrain | 0.17 | 45.22
Afon Teifi/ River Teifi | Poultry | Dofednod | 700to900 | DrainedAr | Afon Teifi/ River TeifiPoultry700to900DrainedAr | 0.61 | 32.91
Afon Teifi/ River Teifi | Poultry | Dofednod | 700to900 | DrainedArGr | Afon Teifi/ River TeifiPoultry700to900DrainedArGr | 0.86 | 28.45
Afon Teifi/ River Teifi | Poultry | Dofednod | 900to1200 | FreeDrain | Afon Teifi/ River TeifiPoultry900to1200FreeDrain | 0.3 | 48.07
Afon Teifi/ River Teifi | Poultry | Dofednod | 900to1200 | DrainedAr | Afon Teifi/ River TeifiPoultry900to1200DrainedAr | 1.15 | 40.53
Afon Teifi/ River Teifi | Poultry | Dofednod | 900to1200 | DrainedArGr | Afon Teifi/ River TeifiPoultry900to1200DrainedArGr | 1.43 | 31.78
Afon Teifi/ River Teifi | Poultry | Dofednod | 1200to1500 | FreeDrain | Afon Teifi/ River TeifiPoultry1200to1500FreeDrain | 0.44 | 49.42
Afon Teifi/ River Teifi | Poultry | Dofednod | 1200to1500 | DrainedAr | Afon Teifi/ River TeifiPoultry1200to1500DrainedAr | 1.83 | 47.69
Afon Teifi/ River Teifi | Poultry | Dofednod | 1200to1500 | DrainedArGr | Afon Teifi/ River TeifiPoultry1200to1500DrainedArGr | 2.07 | 36.54
Afon Teifi/ River Teifi | Poultry | Dofednod | Over1500 | FreeDrain | Afon Teifi/ River TeifiPoultryOver1500FreeDrain | 0.81 | 51.52
Afon Teifi/ River Teifi | Poultry | Dofednod | Over1500 | DrainedAr | Afon Teifi/ River TeifiPoultryOver1500DrainedAr | 2.48 | 55.52
Afon Teifi/ River Teifi | Poultry | Dofednod | Over1500 | DrainedArGr | Afon Teifi/ River TeifiPoultryOver1500DrainedArGr | 3.89 | 43.26
Afon Teifi/ River Teifi | Dairy | Llaeth | 700to900 | FreeDrain | Afon Teifi/ River TeifiDairy700to900FreeDrain | 0.17 | 26.8
Afon Teifi/ River Teifi | Dairy | Llaeth | 700to900 | DrainedAr | Afon Teifi/ River TeifiDairy700to900DrainedAr | 0.2 | 21.14
Afon Teifi/ River Teifi | Dairy | Llaeth | 700to900 | DrainedArGr | Afon Teifi/ River TeifiDairy700to900DrainedArGr | 0.92 | 13.94
Afon Teifi/ River Teifi | Dairy | Llaeth | 900to1200 | FreeDrain | Afon Teifi/ River TeifiDairy900to1200FreeDrain | 0.24 | 28.47
Afon Teifi/ River Teifi | Dairy | Llaeth | 900to1200 | DrainedAr | Afon Teifi/ River TeifiDairy900to1200DrainedAr | 0.29 | 26.81
Afon Teifi/ River Teifi | Dairy | Llaeth | 900to1200 | DrainedArGr | Afon Teifi/ River TeifiDairy900to1200DrainedArGr | 1.46 | 19.39
Afon Teifi/ River Teifi | Dairy | Llaeth | 1200to1500 | FreeDrain | Afon Teifi/ River TeifiDairy1200to1500FreeDrain | 0.31 | 27.88
Afon Teifi/ River Teifi | Dairy | Llaeth | 1200to1500 | DrainedAr | Afon Teifi/ River TeifiDairy1200to1500DrainedAr | 0.44 | 30.07
Afon Teifi/ River Teifi | Dairy | Llaeth | 1200to1500 | DrainedArGr | Afon Teifi/ River TeifiDairy1200to1500DrainedArGr | 2.07 | 25.25
Afon Teifi/ River Teifi | Dairy | Llaeth | Over1500 | FreeDrain | Afon Teifi/ River TeifiDairyOver1500FreeDrain | 0.46 | 25.73
Afon Teifi/ River Teifi | Dairy | Llaeth | Over1500 | DrainedAr | Afon Teifi/ River TeifiDairyOver1500DrainedAr | 0.54 | 34.04
Afon Teifi/ River Teifi | Dairy | Llaeth | Over1500 | DrainedArGr | Afon Teifi/ River TeifiDairyOver1500DrainedArGr | 2.99 | 33.79
Afon Teifi/ River Teifi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 700to900 | FreeDrain | Afon Teifi/ River TeifiLess Favoured Area grazing700to900FreeDrain | 0.1 | 10.08
Afon Teifi/ River Teifi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 700to900 | DrainedAr | Afon Teifi/ River TeifiLess Favoured Area grazing700to900DrainedAr | 0.1 | 8.18
Afon Teifi/ River Teifi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 700to900 | DrainedArGr | Afon Teifi/ River TeifiLess Favoured Area grazing700to900DrainedArGr | 0.53 | 6.88
Afon Teifi/ River Teifi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | FreeDrain | Afon Teifi/ River TeifiLess Favoured Area grazing900to1200FreeDrain | 0.16 | 10.84
Afon Teifi/ River Teifi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedAr | Afon Teifi/ River TeifiLess Favoured Area grazing900to1200DrainedAr | 0.17 | 10.41
Afon Teifi/ River Teifi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedArGr | Afon Teifi/ River TeifiLess Favoured Area grazing900to1200DrainedArGr | 0.88 | 9.07
Afon Teifi/ River Teifi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | FreeDrain | Afon Teifi/ River TeifiLess Favoured Area grazing1200to1500FreeDrain | 0.23 | 10.64
Afon Teifi/ River Teifi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedAr | Afon Teifi/ River TeifiLess Favoured Area grazing1200to1500DrainedAr | 0.27 | 11.6
Afon Teifi/ River Teifi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedArGr | Afon Teifi/ River TeifiLess Favoured Area grazing1200to1500DrainedArGr | 1.29 | 11.19
Afon Teifi/ River Teifi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | FreeDrain | Afon Teifi/ River TeifiLess Favoured Area grazingOver1500FreeDrain | 0.35 | 9.91
Afon Teifi/ River Teifi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedAr | Afon Teifi/ River TeifiLess Favoured Area grazingOver1500DrainedAr | 0.35 | 12.65
Afon Teifi/ River Teifi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedArGr | Afon Teifi/ River TeifiLess Favoured Area grazingOver1500DrainedArGr | 1.91 | 13.99
Afon Teifi/ River Teifi | Lowland grazing | Pori iseldir | 700to900 | FreeDrain | Afon Teifi/ River TeifiLowland grazing700to900FreeDrain | 0.13 | 14.69
Afon Teifi/ River Teifi | Lowland grazing | Pori iseldir | 700to900 | DrainedAr | Afon Teifi/ River TeifiLowland grazing700to900DrainedAr | 0.15 | 11.61
Afon Teifi/ River Teifi | Lowland grazing | Pori iseldir | 700to900 | DrainedArGr | Afon Teifi/ River TeifiLowland grazing700to900DrainedArGr | 0.73 | 9.03
Afon Teifi/ River Teifi | Lowland grazing | Pori iseldir | 900to1200 | FreeDrain | Afon Teifi/ River TeifiLowland grazing900to1200FreeDrain | 0.19 | 15.83
Afon Teifi/ River Teifi | Lowland grazing | Pori iseldir | 900to1200 | DrainedAr | Afon Teifi/ River TeifiLowland grazing900to1200DrainedAr | 0.24 | 15.01
Afon Teifi/ River Teifi | Lowland grazing | Pori iseldir | 900to1200 | DrainedArGr | Afon Teifi/ River TeifiLowland grazing900to1200DrainedArGr | 1.19 | 12.25
Afon Teifi/ River Teifi | Lowland grazing | Pori iseldir | 1200to1500 | FreeDrain | Afon Teifi/ River TeifiLowland grazing1200to1500FreeDrain | 0.27 | 15.56
Afon Teifi/ River Teifi | Lowland grazing | Pori iseldir | 1200to1500 | DrainedAr | Afon Teifi/ River TeifiLowland grazing1200to1500DrainedAr | 0.37 | 16.95
Afon Teifi/ River Teifi | Lowland grazing | Pori iseldir | 1200to1500 | DrainedArGr | Afon Teifi/ River TeifiLowland grazing1200to1500DrainedArGr | 1.72 | 15.5
Afon Teifi/ River Teifi | Lowland grazing | Pori iseldir | Over1500 | FreeDrain | Afon Teifi/ River TeifiLowland grazingOver1500FreeDrain | 0.41 | 14.42
Afon Teifi/ River Teifi | Lowland grazing | Pori iseldir | Over1500 | DrainedAr | Afon Teifi/ River TeifiLowland grazingOver1500DrainedAr | 0.48 | 18.82
Afon Teifi/ River Teifi | Lowland grazing | Pori iseldir | Over1500 | DrainedArGr | Afon Teifi/ River TeifiLowland grazingOver1500DrainedArGr | 2.53 | 19.68
Afon Teifi/ River Teifi | Mixed | Cymysg | 700to900 | FreeDrain | Afon Teifi/ River TeifiMixed700to900FreeDrain | 0.13 | 16.71
Afon Teifi/ River Teifi | Mixed | Cymysg | 700to900 | DrainedAr | Afon Teifi/ River TeifiMixed700to900DrainedAr | 0.19 | 13.18
Afon Teifi/ River Teifi | Mixed | Cymysg | 700to900 | DrainedArGr | Afon Teifi/ River TeifiMixed700to900DrainedArGr | 0.79 | 10.36
Afon Teifi/ River Teifi | Mixed | Cymysg | 900to1200 | FreeDrain | Afon Teifi/ River TeifiMixed900to1200FreeDrain | 0.2 | 18
Afon Teifi/ River Teifi | Mixed | Cymysg | 900to1200 | DrainedAr | Afon Teifi/ River TeifiMixed900to1200DrainedAr | 0.32 | 17.04
Afon Teifi/ River Teifi | Mixed | Cymysg | 900to1200 | DrainedArGr | Afon Teifi/ River TeifiMixed900to1200DrainedArGr | 1.29 | 14.03
Afon Teifi/ River Teifi | Mixed | Cymysg | 1200to1500 | FreeDrain | Afon Teifi/ River TeifiMixed1200to1500FreeDrain | 0.28 | 17.76
Afon Teifi/ River Teifi | Mixed | Cymysg | 1200to1500 | DrainedAr | Afon Teifi/ River TeifiMixed1200to1500DrainedAr | 0.5 | 19.43
Afon Teifi/ River Teifi | Mixed | Cymysg | 1200to1500 | DrainedArGr | Afon Teifi/ River TeifiMixed1200to1500DrainedArGr | 1.85 | 17.82
Afon Teifi/ River Teifi | Mixed | Cymysg | Over1500 | FreeDrain | Afon Teifi/ River TeifiMixedOver1500FreeDrain | 0.43 | 16.58
Afon Teifi/ River Teifi | Mixed | Cymysg | Over1500 | DrainedAr | Afon Teifi/ River TeifiMixedOver1500DrainedAr | 0.65 | 21.76
Afon Teifi/ River Teifi | Mixed | Cymysg | Over1500 | DrainedArGr | Afon Teifi/ River TeifiMixedOver1500DrainedArGr | 2.78 | 22.82
Afon Teifi/ River Teifi | Outdoor pig farming | Ffermio moch yn yr awyr agored | 700to900 | FreeDrain | Afon Teifi/ River TeifiOutdoor pig farming700to900FreeDrain | 0.24 | 30.45
Afon Teifi/ River Teifi | Outdoor pig farming | Ffermio moch yn yr awyr agored | 700to900 | DrainedAr | Afon Teifi/ River TeifiOutdoor pig farming700to900DrainedAr | 1.1 | 25.73
Afon Teifi/ River Teifi | Outdoor pig farming | Ffermio moch yn yr awyr agored | 700to900 | DrainedArGr | Afon Teifi/ River TeifiOutdoor pig farming700to900DrainedArGr | 1.35 | 24.94
Afon Teifi/ River Teifi | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | FreeDrain | Afon Teifi/ River TeifiOutdoor pig farming900to1200FreeDrain | 0.42 | 32.38
Afon Teifi/ River Teifi | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedAr | Afon Teifi/ River TeifiOutdoor pig farming900to1200DrainedAr | 2.07 | 33.34
Afon Teifi/ River Teifi | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedArGr | Afon Teifi/ River TeifiOutdoor pig farming900to1200DrainedArGr | 2.18 | 29.26
Afon Teifi/ River Teifi | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | FreeDrain | Afon Teifi/ River TeifiOutdoor pig farming1200to1500FreeDrain | 0.62 | 33.13
Afon Teifi/ River Teifi | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedAr | Afon Teifi/ River TeifiOutdoor pig farming1200to1500DrainedAr | 3.3 | 41.19
Afon Teifi/ River Teifi | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedArGr | Afon Teifi/ River TeifiOutdoor pig farming1200to1500DrainedArGr | 3.08 | 35.5
Afon Teifi/ River Teifi | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | FreeDrain | Afon Teifi/ River TeifiOutdoor pig farmingOver1500FreeDrain | 1.17 | 35.41
Afon Teifi/ River Teifi | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedAr | Afon Teifi/ River TeifiOutdoor pig farmingOver1500DrainedAr | 4.34 | 50.83
Afon Teifi/ River Teifi | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedArGr | Afon Teifi/ River TeifiOutdoor pig farmingOver1500DrainedArGr | 6.08 | 45.91
Afon Tywi/ River Tywi | Cereals | Grawnfwydydd | 1200to1500 | FreeDrain | Afon Tywi/ River TywiCereals1200to1500FreeDrain | 0.16 | 7.52
Afon Tywi/ River Tywi | Cereals | Grawnfwydydd | 1200to1500 | DrainedAr | Afon Tywi/ River TywiCereals1200to1500DrainedAr | 0.27 | 8.06
Afon Tywi/ River Tywi | Cereals | Grawnfwydydd | 1200to1500 | DrainedArGr | Afon Tywi/ River TywiCereals1200to1500DrainedArGr | 0.9 | 7.7
Afon Tywi/ River Tywi | Cereals | Grawnfwydydd | Over1500 | FreeDrain | Afon Tywi/ River TywiCerealsOver1500FreeDrain | 0.26 | 7.28
Afon Tywi/ River Tywi | Cereals | Grawnfwydydd | Over1500 | DrainedAr | Afon Tywi/ River TywiCerealsOver1500DrainedAr | 0.36 | 9.03
Afon Tywi/ River Tywi | Cereals | Grawnfwydydd | Over1500 | DrainedArGr | Afon Tywi/ River TywiCerealsOver1500DrainedArGr | 1.42 | 9.79
Afon Tywi/ River Tywi | General cropping | Cnydio cyffredinol | 1200to1500 | FreeDrain | Afon Tywi/ River TywiGeneral cropping1200to1500FreeDrain | 0.17 | 5.63
Afon Tywi/ River Tywi | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedAr | Afon Tywi/ River TywiGeneral cropping1200to1500DrainedAr | 0.31 | 5.97
Afon Tywi/ River Tywi | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedArGr | Afon Tywi/ River TywiGeneral cropping1200to1500DrainedArGr | 0.99 | 5.73
Afon Tywi/ River Tywi | General cropping | Cnydio cyffredinol | Over1500 | FreeDrain | Afon Tywi/ River TywiGeneral croppingOver1500FreeDrain | 0.29 | 5.51
Afon Tywi/ River Tywi | General cropping | Cnydio cyffredinol | Over1500 | DrainedAr | Afon Tywi/ River TywiGeneral croppingOver1500DrainedAr | 0.42 | 6.77
Afon Tywi/ River Tywi | General cropping | Cnydio cyffredinol | Over1500 | DrainedArGr | Afon Tywi/ River TywiGeneral croppingOver1500DrainedArGr | 1.6 | 7.74
Afon Tywi/ River Tywi | Horticulture | Garddwriaeth | 1200to1500 | FreeDrain | Afon Tywi/ River TywiHorticulture1200to1500FreeDrain | 0.18 | 7.05
Afon Tywi/ River Tywi | Horticulture | Garddwriaeth | 1200to1500 | DrainedAr | Afon Tywi/ River TywiHorticulture1200to1500DrainedAr | 0.43 | 7.42
Afon Tywi/ River Tywi | Horticulture | Garddwriaeth | 1200to1500 | DrainedArGr | Afon Tywi/ River TywiHorticulture1200to1500DrainedArGr | 0.98 | 6.87
Afon Tywi/ River Tywi | Horticulture | Garddwriaeth | Over1500 | FreeDrain | Afon Tywi/ River TywiHorticultureOver1500FreeDrain | 0.32 | 7.05
Afon Tywi/ River Tywi | Horticulture | Garddwriaeth | Over1500 | DrainedAr | Afon Tywi/ River TywiHorticultureOver1500DrainedAr | 0.59 | 8.51
Afon Tywi/ River Tywi | Horticulture | Garddwriaeth | Over1500 | DrainedArGr | Afon Tywi/ River TywiHorticultureOver1500DrainedArGr | 1.65 | 8.96
Afon Tywi/ River Tywi | Indoor pig farming | Ffermio moch dan do | 1200to1500 | FreeDrain | Afon Tywi/ River TywiIndoor pig farming1200to1500FreeDrain | 0.42 | 24.11
Afon Tywi/ River Tywi | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedAr | Afon Tywi/ River TywiIndoor pig farming1200to1500DrainedAr | 1.75 | 25.76
Afon Tywi/ River Tywi | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedArGr | Afon Tywi/ River TywiIndoor pig farming1200to1500DrainedArGr | 1.99 | 20.89
Afon Tywi/ River Tywi | Indoor pig farming | Ffermio moch dan do | Over1500 | FreeDrain | Afon Tywi/ River TywiIndoor pig farmingOver1500FreeDrain | 0.77 | 25.01
Afon Tywi/ River Tywi | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedAr | Afon Tywi/ River TywiIndoor pig farmingOver1500DrainedAr | 2.37 | 30.82
Afon Tywi/ River Tywi | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedArGr | Afon Tywi/ River TywiIndoor pig farmingOver1500DrainedArGr | 3.77 | 26.23
Afon Tywi/ River Tywi | Poultry | Dofednod | 1200to1500 | FreeDrain | Afon Tywi/ River TywiPoultry1200to1500FreeDrain | 0.41 | 60.55
Afon Tywi/ River Tywi | Poultry | Dofednod | 1200to1500 | DrainedAr | Afon Tywi/ River TywiPoultry1200to1500DrainedAr | 1.46 | 56.91
Afon Tywi/ River Tywi | Poultry | Dofednod | 1200to1500 | DrainedArGr | Afon Tywi/ River TywiPoultry1200to1500DrainedArGr | 2.07 | 42.15
Afon Tywi/ River Tywi | Poultry | Dofednod | Over1500 | FreeDrain | Afon Tywi/ River TywiPoultryOver1500FreeDrain | 0.73 | 62.58
Afon Tywi/ River Tywi | Poultry | Dofednod | Over1500 | DrainedAr | Afon Tywi/ River TywiPoultryOver1500DrainedAr | 1.98 | 65.47
Afon Tywi/ River Tywi | Poultry | Dofednod | Over1500 | DrainedArGr | Afon Tywi/ River TywiPoultryOver1500DrainedArGr | 3.64 | 49.17
Afon Tywi/ River Tywi | Dairy | Llaeth | 1200to1500 | FreeDrain | Afon Tywi/ River TywiDairy1200to1500FreeDrain | 0.27 | 20.67
Afon Tywi/ River Tywi | Dairy | Llaeth | 1200to1500 | DrainedAr | Afon Tywi/ River TywiDairy1200to1500DrainedAr | 0.36 | 22.44
Afon Tywi/ River Tywi | Dairy | Llaeth | 1200to1500 | DrainedArGr | Afon Tywi/ River TywiDairy1200to1500DrainedArGr | 1.8 | 20.59
Afon Tywi/ River Tywi | Dairy | Llaeth | Over1500 | FreeDrain | Afon Tywi/ River TywiDairyOver1500FreeDrain | 0.4 | 19.22
Afon Tywi/ River Tywi | Dairy | Llaeth | Over1500 | DrainedAr | Afon Tywi/ River TywiDairyOver1500DrainedAr | 0.46 | 25.39
Afon Tywi/ River Tywi | Dairy | Llaeth | Over1500 | DrainedArGr | Afon Tywi/ River TywiDairyOver1500DrainedArGr | 2.63 | 28.06
Afon Tywi/ River Tywi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | FreeDrain | Afon Tywi/ River TywiLess Favoured Area grazing1200to1500FreeDrain | 0.23 | 11.27
Afon Tywi/ River Tywi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedAr | Afon Tywi/ River TywiLess Favoured Area grazing1200to1500DrainedAr | 0.28 | 12.35
Afon Tywi/ River Tywi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedArGr | Afon Tywi/ River TywiLess Favoured Area grazing1200to1500DrainedArGr | 1.36 | 12.31
Afon Tywi/ River Tywi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | FreeDrain | Afon Tywi/ River TywiLess Favoured Area grazingOver1500FreeDrain | 0.36 | 10.51
Afon Tywi/ River Tywi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedAr | Afon Tywi/ River TywiLess Favoured Area grazingOver1500DrainedAr | 0.36 | 13.43
Afon Tywi/ River Tywi | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedArGr | Afon Tywi/ River TywiLess Favoured Area grazingOver1500DrainedArGr | 1.99 | 15.33
Afon Tywi/ River Tywi | Lowland grazing | Pori iseldir | 1200to1500 | FreeDrain | Afon Tywi/ River TywiLowland grazing1200to1500FreeDrain | 0.26 | 14.67
Afon Tywi/ River Tywi | Lowland grazing | Pori iseldir | 1200to1500 | DrainedAr | Afon Tywi/ River TywiLowland grazing1200to1500DrainedAr | 0.35 | 16.06
Afon Tywi/ River Tywi | Lowland grazing | Pori iseldir | 1200to1500 | DrainedArGr | Afon Tywi/ River TywiLowland grazing1200to1500DrainedArGr | 1.69 | 15.36
Afon Tywi/ River Tywi | Lowland grazing | Pori iseldir | Over1500 | FreeDrain | Afon Tywi/ River TywiLowland grazingOver1500FreeDrain | 0.39 | 13.61
Afon Tywi/ River Tywi | Lowland grazing | Pori iseldir | Over1500 | DrainedAr | Afon Tywi/ River TywiLowland grazingOver1500DrainedAr | 0.45 | 17.75
Afon Tywi/ River Tywi | Lowland grazing | Pori iseldir | Over1500 | DrainedArGr | Afon Tywi/ River TywiLowland grazingOver1500DrainedArGr | 2.48 | 19.41
Afon Tywi/ River Tywi | Mixed | Cymysg | 1200to1500 | FreeDrain | Afon Tywi/ River TywiMixed1200to1500FreeDrain | 0.25 | 15.59
Afon Tywi/ River Tywi | Mixed | Cymysg | 1200to1500 | DrainedAr | Afon Tywi/ River TywiMixed1200to1500DrainedAr | 0.39 | 17.06
Afon Tywi/ River Tywi | Mixed | Cymysg | 1200to1500 | DrainedArGr | Afon Tywi/ River TywiMixed1200to1500DrainedArGr | 1.73 | 16.48
Afon Tywi/ River Tywi | Mixed | Cymysg | Over1500 | FreeDrain | Afon Tywi/ River TywiMixedOver1500FreeDrain | 0.39 | 14.5
Afon Tywi/ River Tywi | Mixed | Cymysg | Over1500 | DrainedAr | Afon Tywi/ River TywiMixedOver1500DrainedAr | 0.5 | 18.9
Afon Tywi/ River Tywi | Mixed | Cymysg | Over1500 | DrainedArGr | Afon Tywi/ River TywiMixedOver1500DrainedArGr | 2.54 | 21.01
Afon Tywi/ River Tywi | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | FreeDrain | Afon Tywi/ River TywiOutdoor pig farming1200to1500FreeDrain | 0.71 | 23.3
Afon Tywi/ River Tywi | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedAr | Afon Tywi/ River TywiOutdoor pig farming1200to1500DrainedAr | 3.93 | 27.49
Afon Tywi/ River Tywi | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedArGr | Afon Tywi/ River TywiOutdoor pig farming1200to1500DrainedArGr | 3.66 | 22.54
Afon Tywi/ River Tywi | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | FreeDrain | Afon Tywi/ River TywiOutdoor pig farmingOver1500FreeDrain | 1.37 | 24.61
Afon Tywi/ River Tywi | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedAr | Afon Tywi/ River TywiOutdoor pig farmingOver1500DrainedAr | 5.09 | 33.38
Afon Tywi/ River Tywi | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedArGr | Afon Tywi/ River TywiOutdoor pig farmingOver1500DrainedArGr | 7.16 | 28.53
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Cereals | Grawnfwydydd | 900to1200 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineCereals900to1200FreeDrain | 0.26 | 20.87
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Cereals | Grawnfwydydd | 900to1200 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineCereals900to1200DrainedAr | 1.01 | 19.87
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Cereals | Grawnfwydydd | 900to1200 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineCereals900to1200DrainedArGr | 1.26 | 16.68
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Cereals | Grawnfwydydd | 1200to1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineCereals1200to1500FreeDrain | 0.39 | 21.57
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Cereals | Grawnfwydydd | 1200to1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineCereals1200to1500DrainedAr | 1.63 | 24.42
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Cereals | Grawnfwydydd | 1200to1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineCereals1200to1500DrainedArGr | 1.86 | 20.29
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Cereals | Grawnfwydydd | Over1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineCerealsOver1500FreeDrain | 0.72 | 22.45
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Cereals | Grawnfwydydd | Over1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineCerealsOver1500DrainedAr | 2.21 | 29.47
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Cereals | Grawnfwydydd | Over1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineCerealsOver1500DrainedArGr | 3.52 | 25.79
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | General cropping | Cnydio cyffredinol | 900to1200 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineGeneral cropping900to1200FreeDrain | 0.24 | 15.61
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | General cropping | Cnydio cyffredinol | 900to1200 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineGeneral cropping900to1200DrainedAr | 0.86 | 14.02
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | General cropping | Cnydio cyffredinol | 900to1200 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineGeneral cropping900to1200DrainedArGr | 1.19 | 11.4
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | General cropping | Cnydio cyffredinol | 1200to1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineGeneral cropping1200to1500FreeDrain | 0.37 | 16.05
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineGeneral cropping1200to1500DrainedAr | 1.4 | 17.02
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineGeneral cropping1200to1500DrainedArGr | 1.77 | 13.82
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | General cropping | Cnydio cyffredinol | Over1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineGeneral croppingOver1500FreeDrain | 0.67 | 16.42
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | General cropping | Cnydio cyffredinol | Over1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineGeneral croppingOver1500DrainedAr | 1.91 | 20.18
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | General cropping | Cnydio cyffredinol | Over1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineGeneral croppingOver1500DrainedArGr | 3.29 | 17.5
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Horticulture | Garddwriaeth | 900to1200 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineHorticulture900to1200FreeDrain | 0.31 | 21.85
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Horticulture | Garddwriaeth | 900to1200 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineHorticulture900to1200DrainedAr | 1.25 | 19.49
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Horticulture | Garddwriaeth | 900to1200 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineHorticulture900to1200DrainedArGr | 1.47 | 15.79
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Horticulture | Garddwriaeth | 1200to1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineHorticulture1200to1500FreeDrain | 0.47 | 22.39
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Horticulture | Garddwriaeth | 1200to1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineHorticulture1200to1500DrainedAr | 2.02 | 23.65
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Horticulture | Garddwriaeth | 1200to1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineHorticulture1200to1500DrainedArGr | 2.16 | 18.63
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Horticulture | Garddwriaeth | Over1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineHorticultureOver1500FreeDrain | 0.88 | 23.08
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Horticulture | Garddwriaeth | Over1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineHorticultureOver1500DrainedAr | 2.76 | 28.2
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Horticulture | Garddwriaeth | Over1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineHorticultureOver1500DrainedArGr | 4.17 | 23.15
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Indoor pig farming | Ffermio moch dan do | 900to1200 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineIndoor pig farming900to1200FreeDrain | - | -
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineIndoor pig farming900to1200DrainedAr | - | -
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineIndoor pig farming900to1200DrainedArGr | - | -
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Indoor pig farming | Ffermio moch dan do | 1200to1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineIndoor pig farming1200to1500FreeDrain | - | -
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineIndoor pig farming1200to1500DrainedAr | - | -
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineIndoor pig farming1200to1500DrainedArGr | - | -
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Indoor pig farming | Ffermio moch dan do | Over1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineIndoor pig farmingOver1500FreeDrain | - | -
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineIndoor pig farmingOver1500DrainedAr | - | -
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineIndoor pig farmingOver1500DrainedArGr | - | -
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Poultry | Dofednod | 900to1200 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarinePoultry900to1200FreeDrain | 0.33 | 66.62
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Poultry | Dofednod | 900to1200 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarinePoultry900to1200DrainedAr | 1.1 | 56.48
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Poultry | Dofednod | 900to1200 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarinePoultry900to1200DrainedArGr | 1.51 | 43.4
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Poultry | Dofednod | 1200to1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarinePoultry1200to1500FreeDrain | 0.47 | 68.22
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Poultry | Dofednod | 1200to1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarinePoultry1200to1500DrainedAr | 1.72 | 65.42
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Poultry | Dofednod | 1200to1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarinePoultry1200to1500DrainedArGr | 2.17 | 49.48
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Poultry | Dofednod | Over1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarinePoultryOver1500FreeDrain | 0.84 | 70.87
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Poultry | Dofednod | Over1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarinePoultryOver1500DrainedAr | 2.36 | 75.37
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Poultry | Dofednod | Over1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarinePoultryOver1500DrainedArGr | 3.91 | 57.63
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Dairy | Llaeth | 900to1200 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineDairy900to1200FreeDrain | 0.36 | 42.04
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Dairy | Llaeth | 900to1200 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineDairy900to1200DrainedAr | 0.6 | 39.48
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Dairy | Llaeth | 900to1200 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineDairy900to1200DrainedArGr | 2.04 | 28.34
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Dairy | Llaeth | 1200to1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineDairy1200to1500FreeDrain | 0.46 | 41.27
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Dairy | Llaeth | 1200to1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineDairy1200to1500DrainedAr | 0.9 | 44.45
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Dairy | Llaeth | 1200to1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineDairy1200to1500DrainedArGr | 2.8 | 35.8
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Dairy | Llaeth | Over1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineDairyOver1500FreeDrain | 0.68 | 38.51
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Dairy | Llaeth | Over1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineDairyOver1500DrainedAr | 1.13 | 50.49
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Dairy | Llaeth | Over1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineDairyOver1500DrainedArGr | 4.1 | 46.48
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLess Favoured Area grazing900to1200FreeDrain | 0.17 | 10.27
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLess Favoured Area grazing900to1200DrainedAr | 0.18 | 9.83
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLess Favoured Area grazing900to1200DrainedArGr | 0.95 | 8.35
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLess Favoured Area grazing1200to1500FreeDrain | 0.24 | 10.16
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLess Favoured Area grazing1200to1500DrainedAr | 0.29 | 11.1
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLess Favoured Area grazing1200to1500DrainedArGr | 1.41 | 10.63
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLess Favoured Area grazingOver1500FreeDrain | 0.37 | 9.55
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLess Favoured Area grazingOver1500DrainedAr | 0.38 | 12.3
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLess Favoured Area grazingOver1500DrainedArGr | 2.09 | 13.74
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Lowland grazing | Pori iseldir | 900to1200 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLowland grazing900to1200FreeDrain | 0.27 | 20.17
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Lowland grazing | Pori iseldir | 900to1200 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLowland grazing900to1200DrainedAr | 0.59 | 18.54
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Lowland grazing | Pori iseldir | 900to1200 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLowland grazing900to1200DrainedArGr | 1.34 | 14.55
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Lowland grazing | Pori iseldir | 1200to1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLowland grazing1200to1500FreeDrain | 0.38 | 20.21
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Lowland grazing | Pori iseldir | 1200to1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLowland grazing1200to1500DrainedAr | 0.94 | 21.34
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Lowland grazing | Pori iseldir | 1200to1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLowland grazing1200to1500DrainedArGr | 1.94 | 17.84
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Lowland grazing | Pori iseldir | Over1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLowland grazingOver1500FreeDrain | 0.62 | 19.67
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Lowland grazing | Pori iseldir | Over1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLowland grazingOver1500DrainedAr | 1.26 | 24.35
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Lowland grazing | Pori iseldir | Over1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineLowland grazingOver1500DrainedArGr | 3.13 | 22.32
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Mixed | Cymysg | 900to1200 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineMixed900to1200FreeDrain | 0.26 | 21.62
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Mixed | Cymysg | 900to1200 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineMixed900to1200DrainedAr | 0.64 | 20.16
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Mixed | Cymysg | 900to1200 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineMixed900to1200DrainedArGr | 1.41 | 16.39
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Mixed | Cymysg | 1200to1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineMixed1200to1500FreeDrain | 0.36 | 21.58
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Mixed | Cymysg | 1200to1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineMixed1200to1500DrainedAr | 1.02 | 23.41
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Mixed | Cymysg | 1200to1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineMixed1200to1500DrainedArGr | 2.03 | 20.25
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Mixed | Cymysg | Over1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineMixedOver1500FreeDrain | 0.61 | 21.06
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Mixed | Cymysg | Over1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineMixedOver1500DrainedAr | 1.36 | 26.92
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Mixed | Cymysg | Over1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineMixedOver1500DrainedArGr | 3.33 | 25.78
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineOutdoor pig farming900to1200FreeDrain | 0.47 | 26.15
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineOutdoor pig farming900to1200DrainedAr | 2.4 | 26.67
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineOutdoor pig farming900to1200DrainedArGr | 2.54 | 22.67
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineOutdoor pig farming1200to1500FreeDrain | 0.7 | 26.7
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineOutdoor pig farming1200to1500DrainedAr | 3.81 | 32.48
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineOutdoor pig farming1200to1500DrainedArGr | 3.51 | 27.19
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | FreeDrain | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineOutdoor pig farmingOver1500FreeDrain | 1.35 | 28.4
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedAr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineOutdoor pig farmingOver1500DrainedAr | 5 | 39.75
Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire Marine | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedArGr | Afonydd Cleddau a Sir Benfro Forol/ cleddau Rivers and Pembrokshire MarineOutdoor pig farmingOver1500DrainedArGr | 6.91 | 34.76
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cereals | Grawnfwydydd | 1200to1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesCereals1200to1500FreeDrain | 0.35 | 18.68
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cereals | Grawnfwydydd | 1200to1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesCereals1200to1500DrainedAr | 1.39 | 20.37
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cereals | Grawnfwydydd | 1200to1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesCereals1200to1500DrainedArGr | 1.67 | 16.82
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cereals | Grawnfwydydd | Over1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesCerealsOver1500FreeDrain | 0.65 | 19.26
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cereals | Grawnfwydydd | Over1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesCerealsOver1500DrainedAr | 1.9 | 24.31
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Cereals | Grawnfwydydd | Over1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesCerealsOver1500DrainedArGr | 3.13 | 21.15
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | General cropping | Cnydio cyffredinol | 1200to1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesGeneral cropping1200to1500FreeDrain | 0.4 | 18.34
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesGeneral cropping1200to1500DrainedAr | 1.63 | 19.43
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesGeneral cropping1200to1500DrainedArGr | 1.9 | 15.59
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | General cropping | Cnydio cyffredinol | Over1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesGeneral croppingOver1500FreeDrain | 0.75 | 18.84
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | General cropping | Cnydio cyffredinol | Over1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesGeneral croppingOver1500DrainedAr | 2.22 | 23.09
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | General cropping | Cnydio cyffredinol | Over1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesGeneral croppingOver1500DrainedArGr | 3.6 | 19.55
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Horticulture | Garddwriaeth | 1200to1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesHorticulture1200to1500FreeDrain | 0.48 | 22.73
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Horticulture | Garddwriaeth | 1200to1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesHorticulture1200to1500DrainedAr | 2.08 | 24.05
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Horticulture | Garddwriaeth | 1200to1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesHorticulture1200to1500DrainedArGr | 2.19 | 18.98
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Horticulture | Garddwriaeth | Over1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesHorticultureOver1500FreeDrain | 0.9 | 23.47
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Horticulture | Garddwriaeth | Over1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesHorticultureOver1500DrainedAr | 2.84 | 28.69
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Horticulture | Garddwriaeth | Over1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesHorticultureOver1500DrainedArGr | 4.24 | 23.55
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Indoor pig farming | Ffermio moch dan do | 1200to1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesIndoor pig farming1200to1500FreeDrain | - | -
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesIndoor pig farming1200to1500DrainedAr | - | -
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesIndoor pig farming1200to1500DrainedArGr | - | -
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Indoor pig farming | Ffermio moch dan do | Over1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesIndoor pig farmingOver1500FreeDrain | - | -
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesIndoor pig farmingOver1500DrainedAr | - | -
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesIndoor pig farmingOver1500DrainedArGr | - | -
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Poultry | Dofednod | 1200to1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesPoultry1200to1500FreeDrain | 0.43 | 23.05
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Poultry | Dofednod | 1200to1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesPoultry1200to1500DrainedAr | 1.81 | 25.03
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Poultry | Dofednod | 1200to1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesPoultry1200to1500DrainedArGr | 2 | 20.56
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Poultry | Dofednod | Over1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesPoultryOver1500FreeDrain | 0.8 | 23.94
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Poultry | Dofednod | Over1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesPoultryOver1500DrainedAr | 2.46 | 30.03
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Poultry | Dofednod | Over1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesPoultryOver1500DrainedArGr | 3.82 | 25.96
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Dairy | Llaeth | 1200to1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesDairy1200to1500FreeDrain | 0.34 | 19.06
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Dairy | Llaeth | 1200to1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesDairy1200to1500DrainedAr | 0.9 | 20.81
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Dairy | Llaeth | 1200to1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesDairy1200to1500DrainedArGr | 1.84 | 19.86
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Dairy | Llaeth | Over1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesDairyOver1500FreeDrain | 0.56 | 18.69
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Dairy | Llaeth | Over1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesDairyOver1500DrainedAr | 1.2 | 24.01
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Dairy | Llaeth | Over1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesDairyOver1500DrainedArGr | 3.02 | 26.56
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesLess Favoured Area grazing1200to1500FreeDrain | 0.24 | 10.24
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesLess Favoured Area grazing1200to1500DrainedAr | 0.28 | 11.22
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesLess Favoured Area grazing1200to1500DrainedArGr | 1.35 | 11.21
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesLess Favoured Area grazingOver1500FreeDrain | 0.37 | 9.67
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesLess Favoured Area grazingOver1500DrainedAr | 0.37 | 12.3
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesLess Favoured Area grazingOver1500DrainedArGr | 1.99 | 14.24
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Lowland grazing | Pori iseldir | 1200to1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesLowland grazing1200to1500FreeDrain | 0.35 | 16.73
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Lowland grazing | Pori iseldir | 1200to1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesLowland grazing1200to1500DrainedAr | 1.04 | 17.48
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Lowland grazing | Pori iseldir | 1200to1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesLowland grazing1200to1500DrainedArGr | 1.78 | 14.95
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Lowland grazing | Pori iseldir | Over1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesLowland grazingOver1500FreeDrain | 0.61 | 16.54
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Lowland grazing | Pori iseldir | Over1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesLowland grazingOver1500DrainedAr | 1.41 | 20
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Lowland grazing | Pori iseldir | Over1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesLowland grazingOver1500DrainedArGr | 3.01 | 18.55
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Mixed | Cymysg | 1200to1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesMixed1200to1500FreeDrain | 0.38 | 21.12
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Mixed | Cymysg | 1200to1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesMixed1200to1500DrainedAr | 1.23 | 22.96
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Mixed | Cymysg | 1200to1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesMixed1200to1500DrainedArGr | 2.01 | 19.88
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Mixed | Cymysg | Over1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesMixedOver1500FreeDrain | 0.65 | 20.99
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Mixed | Cymysg | Over1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesMixedOver1500DrainedAr | 1.65 | 26.61
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Mixed | Cymysg | Over1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesMixedOver1500DrainedArGr | 3.42 | 25.01
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesOutdoor pig farming1200to1500FreeDrain | 0.73 | 23.57
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesOutdoor pig farming1200to1500DrainedAr | 4.01 | 28.08
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesOutdoor pig farming1200to1500DrainedArGr | 3.69 | 23.03
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | FreeDrain | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesOutdoor pig farmingOver1500FreeDrain | 1.41 | 24.94
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedAr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesOutdoor pig farmingOver1500DrainedAr | 5.24 | 34.13
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedArGr | Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and EstuariesOutdoor pig farmingOver1500DrainedArGr | 7.25 | 29.18
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cereals | Grawnfwydydd | 900to1200 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesCereals900to1200FreeDrain | 0.08 | 5
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cereals | Grawnfwydydd | 900to1200 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesCereals900to1200DrainedAr | 0.11 | 4.73
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cereals | Grawnfwydydd | 900to1200 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesCereals900to1200DrainedArGr | 0.45 | 3.97
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cereals | Grawnfwydydd | 1200to1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesCereals1200to1500FreeDrain | 0.12 | 6.03
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cereals | Grawnfwydydd | 1200to1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesCereals1200to1500DrainedAr | 0.19 | 6.34
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cereals | Grawnfwydydd | 1200to1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesCereals1200to1500DrainedArGr | 0.69 | 6.1
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cereals | Grawnfwydydd | Over1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesCerealsOver1500FreeDrain | 0.21 | 5.89
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cereals | Grawnfwydydd | Over1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesCerealsOver1500DrainedAr | 0.26 | 7.02
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cereals | Grawnfwydydd | Over1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesCerealsOver1500DrainedArGr | 1.1 | 7.63
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | General cropping | Cnydio cyffredinol | 900to1200 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesGeneral cropping900to1200FreeDrain | 0.1 | 4.28
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | General cropping | Cnydio cyffredinol | 900to1200 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesGeneral cropping900to1200DrainedAr | 0.13 | 4.01
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | General cropping | Cnydio cyffredinol | 900to1200 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesGeneral cropping900to1200DrainedArGr | 0.54 | 3.35
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | General cropping | Cnydio cyffredinol | 1200to1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesGeneral cropping1200to1500FreeDrain | 0.15 | 5
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesGeneral cropping1200to1500DrainedAr | 0.22 | 5.27
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesGeneral cropping1200to1500DrainedArGr | 0.84 | 5.18
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | General cropping | Cnydio cyffredinol | Over1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesGeneral croppingOver1500FreeDrain | 0.25 | 4.89
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | General cropping | Cnydio cyffredinol | Over1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesGeneral croppingOver1500DrainedAr | 0.31 | 5.9
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | General cropping | Cnydio cyffredinol | Over1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesGeneral croppingOver1500DrainedArGr | 1.35 | 6.9
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Horticulture | Garddwriaeth | 900to1200 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesHorticulture900to1200FreeDrain | 0.09 | 4.6
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Horticulture | Garddwriaeth | 900to1200 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesHorticulture900to1200DrainedAr | 0.15 | 4.29
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Horticulture | Garddwriaeth | 900to1200 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesHorticulture900to1200DrainedArGr | 0.48 | 3.65
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Horticulture | Garddwriaeth | 1200to1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesHorticulture1200to1500FreeDrain | 0.14 | 5.57
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Horticulture | Garddwriaeth | 1200to1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesHorticulture1200to1500DrainedAr | 0.25 | 5.82
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Horticulture | Garddwriaeth | 1200to1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesHorticulture1200to1500DrainedArGr | 0.76 | 5.65
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Horticulture | Garddwriaeth | Over1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesHorticultureOver1500FreeDrain | 0.24 | 5.54
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Horticulture | Garddwriaeth | Over1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesHorticultureOver1500DrainedAr | 0.35 | 6.54
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Horticulture | Garddwriaeth | Over1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesHorticultureOver1500DrainedArGr | 1.23 | 7.28
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Indoor pig farming | Ffermio moch dan do | 900to1200 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesIndoor pig farming900to1200FreeDrain | 0.29 | 31.63
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesIndoor pig farming900to1200DrainedAr | 1.11 | 27.97
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesIndoor pig farming900to1200DrainedArGr | 1.46 | 22.22
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Indoor pig farming | Ffermio moch dan do | 1200to1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesIndoor pig farming1200to1500FreeDrain | 0.43 | 32.62
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesIndoor pig farming1200to1500DrainedAr | 1.78 | 33.49
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesIndoor pig farming1200to1500DrainedArGr | 2.1 | 26.22
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Indoor pig farming | Ffermio moch dan do | Over1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesIndoor pig farmingOver1500FreeDrain | 0.79 | 33.89
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesIndoor pig farmingOver1500DrainedAr | 2.41 | 39.68
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesIndoor pig farmingOver1500DrainedArGr | 3.9 | 32.22
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Poultry | Dofednod | 900to1200 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesPoultry900to1200FreeDrain | 0.28 | 24.15
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Poultry | Dofednod | 900to1200 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesPoultry900to1200DrainedAr | 1.08 | 21.69
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Poultry | Dofednod | 900to1200 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesPoultry900to1200DrainedArGr | 1.34 | 17.87
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Poultry | Dofednod | 1200to1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesPoultry1200to1500FreeDrain | 0.42 | 24.87
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Poultry | Dofednod | 1200to1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesPoultry1200to1500DrainedAr | 1.75 | 26.33
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Poultry | Dofednod | 1200to1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesPoultry1200to1500DrainedArGr | 1.97 | 21.34
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Poultry | Dofednod | Over1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesPoultryOver1500FreeDrain | 0.77 | 25.81
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Poultry | Dofednod | Over1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesPoultryOver1500DrainedAr | 2.38 | 31.43
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Poultry | Dofednod | Over1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesPoultryOver1500DrainedArGr | 3.75 | 26.67
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Dairy | Llaeth | 900to1200 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesDairy900to1200FreeDrain | 0.14 | 9.27
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Dairy | Llaeth | 900to1200 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesDairy900to1200DrainedAr | 0.16 | 8.86
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Dairy | Llaeth | 900to1200 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesDairy900to1200DrainedArGr | 0.84 | 9.1
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Dairy | Llaeth | 1200to1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesDairy1200to1500FreeDrain | 0.21 | 9.31
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Dairy | Llaeth | 1200to1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesDairy1200to1500DrainedAr | 0.27 | 10.32
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Dairy | Llaeth | 1200to1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesDairy1200to1500DrainedArGr | 1.28 | 12.57
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Dairy | Llaeth | Over1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesDairyOver1500FreeDrain | 0.33 | 8.97
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Dairy | Llaeth | Over1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesDairyOver1500DrainedAr | 0.35 | 11.65
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Dairy | Llaeth | Over1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesDairyOver1500DrainedArGr | 1.94 | 17.96
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLess Favoured Area grazing900to1200FreeDrain | 0.13 | 7.05
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLess Favoured Area grazing900to1200DrainedAr | 0.13 | 6.86
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLess Favoured Area grazing900to1200DrainedArGr | 0.46 | 6.25
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLess Favoured Area grazing1200to1500FreeDrain | 0.19 | 7.02
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLess Favoured Area grazing1200to1500DrainedAr | 0.21 | 7.43
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLess Favoured Area grazing1200to1500DrainedArGr | 0.7 | 7.21
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLess Favoured Area grazingOver1500FreeDrain | 0.31 | 6.75
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLess Favoured Area grazingOver1500DrainedAr | 0.29 | 7.86
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLess Favoured Area grazingOver1500DrainedArGr | 1.07 | 8.47
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Lowland grazing | Pori iseldir | 900to1200 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLowland grazing900to1200FreeDrain | 0.15 | 9.33
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Lowland grazing | Pori iseldir | 900to1200 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLowland grazing900to1200DrainedAr | 0.17 | 8.91
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Lowland grazing | Pori iseldir | 900to1200 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLowland grazing900to1200DrainedArGr | 0.82 | 7.63
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Lowland grazing | Pori iseldir | 1200to1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLowland grazing1200to1500FreeDrain | 0.21 | 9.34
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Lowland grazing | Pori iseldir | 1200to1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLowland grazing1200to1500DrainedAr | 0.27 | 10.11
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Lowland grazing | Pori iseldir | 1200to1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLowland grazing1200to1500DrainedArGr | 1.21 | 9.65
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Lowland grazing | Pori iseldir | Over1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLowland grazingOver1500FreeDrain | 0.33 | 8.75
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Lowland grazing | Pori iseldir | Over1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLowland grazingOver1500DrainedAr | 0.35 | 11.09
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Lowland grazing | Pori iseldir | Over1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesLowland grazingOver1500DrainedArGr | 1.81 | 12.16
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Mixed | Cymysg | 900to1200 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesMixed900to1200FreeDrain | 0.14 | 9.58
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Mixed | Cymysg | 900to1200 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesMixed900to1200DrainedAr | 0.18 | 9.11
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Mixed | Cymysg | 900to1200 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesMixed900to1200DrainedArGr | 0.83 | 8.06
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Mixed | Cymysg | 1200to1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesMixed1200to1500FreeDrain | 0.2 | 9.74
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Mixed | Cymysg | 1200to1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesMixed1200to1500DrainedAr | 0.29 | 10.54
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Mixed | Cymysg | 1200to1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesMixed1200to1500DrainedArGr | 1.22 | 10.4
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Mixed | Cymysg | Over1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesMixedOver1500FreeDrain | 0.32 | 9.19
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Mixed | Cymysg | Over1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesMixedOver1500DrainedAr | 0.38 | 11.59
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Mixed | Cymysg | Over1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesMixedOver1500DrainedArGr | 1.84 | 13.24
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesOutdoor pig farming900to1200FreeDrain | 0.47 | 22.87
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesOutdoor pig farming900to1200DrainedAr | 2.48 | 22.8
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesOutdoor pig farming900to1200DrainedArGr | 2.67 | 18.96
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesOutdoor pig farming1200to1500FreeDrain | 0.71 | 23.3
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesOutdoor pig farming1200to1500DrainedAr | 3.93 | 27.49
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesOutdoor pig farming1200to1500DrainedArGr | 3.66 | 22.54
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | FreeDrain | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesOutdoor pig farmingOver1500FreeDrain | 1.37 | 24.61
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedAr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesOutdoor pig farmingOver1500DrainedAr | 5.09 | 33.38
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedArGr | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat SitesOutdoor pig farmingOver1500DrainedArGr | 7.16 | 28.53
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | 600to700 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCereals600to700FreeDrain | 0.04 | 10.12
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | 600to700 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCereals600to700DrainedAr | 0.14 | 7.65
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | 600to700 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCereals600to700DrainedArGr | 0.34 | 8.13
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | 700to900 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCereals700to900FreeDrain | 0.11 | 12.88
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | 700to900 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCereals700to900DrainedAr | 0.31 | 10.43
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | 700to900 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCereals700to900DrainedArGr | 0.6 | 9.42
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | 900to1200 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCereals900to1200FreeDrain | 0.19 | 14.11
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | 900to1200 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCereals900to1200DrainedAr | 0.59 | 13.81
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | 900to1200 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCereals900to1200DrainedArGr | 1.02 | 11.92
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | 1200to1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCereals1200to1500FreeDrain | 0.28 | 14.61
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | 1200to1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCereals1200to1500DrainedAr | 0.94 | 16.92
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | 1200to1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCereals1200to1500DrainedArGr | 1.51 | 15.12
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | Over1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCerealsOver1500FreeDrain | 0.49 | 14.87
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | Over1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCerealsOver1500DrainedAr | 1.26 | 20.11
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cereals | Grawnfwydydd | Over1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidCerealsOver1500DrainedArGr | 2.64 | 19.57
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | 600to700 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral cropping600to700FreeDrain | 0.04 | 5.45
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | 600to700 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral cropping600to700DrainedAr | 0.08 | 3.86
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | 600to700 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral cropping600to700DrainedArGr | 0.26 | 3.64
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | 700to900 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral cropping700to900FreeDrain | 0.09 | 6.9
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | 700to900 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral cropping700to900DrainedAr | 0.18 | 5.35
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | 700to900 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral cropping700to900DrainedArGr | 0.46 | 4.33
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | 900to1200 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral cropping900to1200FreeDrain | 0.15 | 7.55
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | 900to1200 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral cropping900to1200DrainedAr | 0.35 | 6.99
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | 900to1200 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral cropping900to1200DrainedArGr | 0.83 | 5.82
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | 1200to1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral cropping1200to1500FreeDrain | 0.23 | 7.84
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral cropping1200to1500DrainedAr | 0.57 | 8.5
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral cropping1200to1500DrainedArGr | 1.28 | 7.73
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | Over1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral croppingOver1500FreeDrain | 0.4 | 7.8
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | Over1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral croppingOver1500DrainedAr | 0.77 | 9.89
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | General cropping | Cnydio cyffredinol | Over1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidGeneral croppingOver1500DrainedArGr | 2.15 | 10.41
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | 600to700 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticulture600to700FreeDrain | 0.04 | 6.92
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | 600to700 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticulture600to700DrainedAr | 0.11 | 4.89
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | 600to700 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticulture600to700DrainedArGr | 0.28 | 4.76
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | 700to900 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticulture700to900FreeDrain | 0.09 | 8.58
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | 700to900 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticulture700to900DrainedAr | 0.24 | 6.53
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | 700to900 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticulture700to900DrainedArGr | 0.5 | 5.47
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | 900to1200 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticulture900to1200FreeDrain | 0.17 | 9.44
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | 900to1200 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticulture900to1200DrainedAr | 0.47 | 8.52
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | 900to1200 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticulture900to1200DrainedArGr | 0.89 | 7.05
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | 1200to1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticulture1200to1500FreeDrain | 0.26 | 9.87
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | 1200to1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticulture1200to1500DrainedAr | 0.76 | 10.43
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | 1200to1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticulture1200to1500DrainedArGr | 1.35 | 9.11
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | Over1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticultureOver1500FreeDrain | 0.45 | 9.94
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | Over1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticultureOver1500DrainedAr | 1.03 | 12.18
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Horticulture | Garddwriaeth | Over1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidHorticultureOver1500DrainedArGr | 2.36 | 11.9
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | 600to700 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farming600to700FreeDrain | 0.05 | 22.11
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | 600to700 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farming600to700DrainedAr | 0.25 | 15.89
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | 600to700 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farming600to700DrainedArGr | 0.5 | 16.08
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | 700to900 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farming700to900FreeDrain | 0.15 | 26.61
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | 700to900 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farming700to900DrainedAr | 0.57 | 20.14
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | 700to900 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farming700to900DrainedArGr | 0.86 | 17.65
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | 900to1200 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farming900to1200FreeDrain | 0.28 | 28.55
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farming900to1200DrainedAr | 1.1 | 25.42
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farming900to1200DrainedArGr | 1.42 | 20.43
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | 1200to1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farming1200to1500FreeDrain | 0.42 | 29.43
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farming1200to1500DrainedAr | 1.77 | 30.59
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farming1200to1500DrainedArGr | 2.06 | 24.22
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | Over1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farmingOver1500FreeDrain | 0.78 | 30.56
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farmingOver1500DrainedAr | 2.4 | 36.36
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidIndoor pig farmingOver1500DrainedArGr | 3.85 | 29.98
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | 600to700 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultry600to700FreeDrain | 0.07 | 42.5
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | 600to700 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultry600to700DrainedAr | 0.15 | 28.87
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | 600to700 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultry600to700DrainedArGr | 0.57 | 25.17
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | 700to900 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultry700to900FreeDrain | 0.14 | 52.13
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | 700to900 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultry700to900DrainedAr | 0.28 | 38.38
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | 700to900 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultry700to900DrainedArGr | 0.86 | 28.15
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | 900to1200 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultry900to1200FreeDrain | 0.23 | 54.9
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | 900to1200 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultry900to1200DrainedAr | 0.47 | 46.52
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | 900to1200 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultry900to1200DrainedArGr | 1.36 | 32.18
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | 1200to1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultry1200to1500FreeDrain | 0.32 | 55.43
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | 1200to1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultry1200to1500DrainedAr | 0.73 | 52.57
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | 1200to1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultry1200to1500DrainedArGr | 1.95 | 37.32
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | Over1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultryOver1500FreeDrain | 0.53 | 55.53
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | Over1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultryOver1500DrainedAr | 0.98 | 59.86
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Poultry | Dofednod | Over1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidPoultryOver1500DrainedArGr | 3.03 | 43.97
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | 600to700 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairy600to700FreeDrain | 0.09 | 14.18
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | 600to700 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairy600to700DrainedAr | 0.11 | 9.72
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | 600to700 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairy600to700DrainedArGr | 0.51 | 8.81
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | 700to900 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairy700to900FreeDrain | 0.14 | 19.79
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | 700to900 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairy700to900DrainedAr | 0.18 | 15.64
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | 700to900 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairy700to900DrainedArGr | 0.78 | 11.29
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | 900to1200 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairy900to1200FreeDrain | 0.21 | 21.05
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | 900to1200 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairy900to1200DrainedAr | 0.28 | 19.85
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | 900to1200 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairy900to1200DrainedArGr | 1.26 | 15.82
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | 1200to1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairy1200to1500FreeDrain | 0.28 | 20.68
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | 1200to1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairy1200to1500DrainedAr | 0.44 | 22.45
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | 1200to1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairy1200to1500DrainedArGr | 1.82 | 20.81
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | Over1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairyOver1500FreeDrain | 0.43 | 19.33
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | Over1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairyOver1500DrainedAr | 0.56 | 25.45
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Dairy | Llaeth | Over1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidDairyOver1500DrainedArGr | 2.71 | 28.33
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 600to700 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazing600to700FreeDrain | 0.05 | 6.97
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 600to700 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazing600to700DrainedAr | 0.06 | 5.13
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 600to700 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazing600to700DrainedArGr | 0.31 | 5.61
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 700to900 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazing700to900FreeDrain | 0.1 | 9.9
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 700to900 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazing700to900DrainedAr | 0.1 | 8.19
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 700to900 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazing700to900DrainedArGr | 0.47 | 7.29
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazing900to1200FreeDrain | 0.15 | 10.65
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazing900to1200DrainedAr | 0.16 | 10.28
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazing900to1200DrainedArGr | 0.77 | 9.34
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazing1200to1500FreeDrain | 0.22 | 10.48
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazing1200to1500DrainedAr | 0.26 | 11.37
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazing1200to1500DrainedArGr | 1.12 | 11.2
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazingOver1500FreeDrain | 0.35 | 9.89
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazingOver1500DrainedAr | 0.34 | 12.25
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLess Favoured Area grazingOver1500DrainedArGr | 1.65 | 13.65
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | 600to700 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazing600to700FreeDrain | 0.07 | 10.27
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | 600to700 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazing600to700DrainedAr | 0.1 | 7.13
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | 600to700 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazing600to700DrainedArGr | 0.49 | 7.7
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | 700to900 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazing700to900FreeDrain | 0.13 | 14.85
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | 700to900 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazing700to900DrainedAr | 0.16 | 11.77
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | 700to900 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazing700to900DrainedArGr | 0.75 | 9.7
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | 900to1200 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazing900to1200FreeDrain | 0.2 | 16.04
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | 900to1200 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazing900to1200DrainedAr | 0.25 | 15.22
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | 900to1200 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazing900to1200DrainedArGr | 1.21 | 12.96
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | 1200to1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazing1200to1500FreeDrain | 0.27 | 15.74
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | 1200to1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazing1200to1500DrainedAr | 0.4 | 17.18
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | 1200to1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazing1200to1500DrainedArGr | 1.74 | 16.2
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | Over1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazingOver1500FreeDrain | 0.42 | 14.65
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | Over1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazingOver1500DrainedAr | 0.51 | 19
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Lowland grazing | Pori iseldir | Over1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidLowland grazingOver1500DrainedArGr | 2.55 | 20.4
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | 600to700 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixed600to700FreeDrain | 0.07 | 12.1
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | 600to700 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixed600to700DrainedAr | 0.12 | 8.47
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | 600to700 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixed600to700DrainedArGr | 0.53 | 9.07
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | 700to900 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixed700to900FreeDrain | 0.13 | 16.88
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | 700to900 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixed700to900DrainedAr | 0.23 | 13.3
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | 700to900 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixed700to900DrainedArGr | 0.82 | 11.16
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | 900to1200 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixed900to1200FreeDrain | 0.21 | 18.18
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | 900to1200 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixed900to1200DrainedAr | 0.4 | 17.16
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | 900to1200 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixed900to1200DrainedArGr | 1.33 | 14.7
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | 1200to1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixed1200to1500FreeDrain | 0.29 | 17.96
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | 1200to1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixed1200to1500DrainedAr | 0.64 | 19.66
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | 1200to1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixed1200to1500DrainedArGr | 1.9 | 18.4
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | Over1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixedOver1500FreeDrain | 0.47 | 17.01
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | Over1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixedOver1500DrainedAr | 0.83 | 22.09
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Mixed | Cymysg | Over1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidMixedOver1500DrainedArGr | 2.92 | 23.4
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | 600to700 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farming600to700FreeDrain | 0.07 | 26.56
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | 600to700 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farming600to700DrainedAr | 0.45 | 21.55
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | 600to700 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farming600to700DrainedArGr | 0.7 | 23.66
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | 700to900 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farming700to900FreeDrain | 0.24 | 32.04
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | 700to900 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farming700to900DrainedAr | 1.05 | 27.14
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | 700to900 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farming700to900DrainedArGr | 1.28 | 26.5
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farming900to1200FreeDrain | 0.41 | 34.13
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farming900to1200DrainedAr | 1.99 | 35.27
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farming900to1200DrainedArGr | 2.09 | 31.14
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farming1200to1500FreeDrain | 0.6 | 34.94
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farming1200to1500DrainedAr | 3.19 | 43.7
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farming1200to1500DrainedArGr | 2.98 | 37.88
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | FreeDrain | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farmingOver1500FreeDrain | 1.13 | 37.39
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedAr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farmingOver1500DrainedAr | 4.2 | 54.02
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedArGr | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn TegidOutdoor pig farmingOver1500DrainedArGr | 5.88 | 49.1
River Usk/ Afon Wysg | Cereals | Grawnfwydydd | 900to1200 | FreeDrain | River Usk/ Afon WysgCereals900to1200FreeDrain | 0.19 | 14.9
River Usk/ Afon Wysg | Cereals | Grawnfwydydd | 900to1200 | DrainedAr | River Usk/ Afon WysgCereals900to1200DrainedAr | 0.62 | 14.62
River Usk/ Afon Wysg | Cereals | Grawnfwydydd | 900to1200 | DrainedArGr | River Usk/ Afon WysgCereals900to1200DrainedArGr | 0.99 | 12.71
River Usk/ Afon Wysg | Cereals | Grawnfwydydd | 1200to1500 | FreeDrain | River Usk/ Afon WysgCereals1200to1500FreeDrain | 0.27 | 15.63
River Usk/ Afon Wysg | Cereals | Grawnfwydydd | 1200to1500 | DrainedAr | River Usk/ Afon WysgCereals1200to1500DrainedAr | 0.99 | 18.11
River Usk/ Afon Wysg | Cereals | Grawnfwydydd | 1200to1500 | DrainedArGr | River Usk/ Afon WysgCereals1200to1500DrainedArGr | 1.46 | 16.15
River Usk/ Afon Wysg | Cereals | Grawnfwydydd | Over1500 | FreeDrain | River Usk/ Afon WysgCerealsOver1500FreeDrain | 0.49 | 16.01
River Usk/ Afon Wysg | Cereals | Grawnfwydydd | Over1500 | DrainedAr | River Usk/ Afon WysgCerealsOver1500DrainedAr | 1.33 | 21.54
River Usk/ Afon Wysg | Cereals | Grawnfwydydd | Over1500 | DrainedArGr | River Usk/ Afon WysgCerealsOver1500DrainedArGr | 2.59 | 20.66
River Usk/ Afon Wysg | General cropping | Cnydio cyffredinol | 900to1200 | FreeDrain | River Usk/ Afon WysgGeneral cropping900to1200FreeDrain | 0.15 | 7.81
River Usk/ Afon Wysg | General cropping | Cnydio cyffredinol | 900to1200 | DrainedAr | River Usk/ Afon WysgGeneral cropping900to1200DrainedAr | 0.36 | 7.24
River Usk/ Afon Wysg | General cropping | Cnydio cyffredinol | 900to1200 | DrainedArGr | River Usk/ Afon WysgGeneral cropping900to1200DrainedArGr | 0.78 | 5.99
River Usk/ Afon Wysg | General cropping | Cnydio cyffredinol | 1200to1500 | FreeDrain | River Usk/ Afon WysgGeneral cropping1200to1500FreeDrain | 0.22 | 8.3
River Usk/ Afon Wysg | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedAr | River Usk/ Afon WysgGeneral cropping1200to1500DrainedAr | 0.59 | 8.97
River Usk/ Afon Wysg | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedArGr | River Usk/ Afon WysgGeneral cropping1200to1500DrainedArGr | 1.19 | 8.01
River Usk/ Afon Wysg | General cropping | Cnydio cyffredinol | Over1500 | FreeDrain | River Usk/ Afon WysgGeneral croppingOver1500FreeDrain | 0.38 | 8.32
River Usk/ Afon Wysg | General cropping | Cnydio cyffredinol | Over1500 | DrainedAr | River Usk/ Afon WysgGeneral croppingOver1500DrainedAr | 0.8 | 10.45
River Usk/ Afon Wysg | General cropping | Cnydio cyffredinol | Over1500 | DrainedArGr | River Usk/ Afon WysgGeneral croppingOver1500DrainedArGr | 2.04 | 10.55
River Usk/ Afon Wysg | Horticulture | Garddwriaeth | 900to1200 | FreeDrain | River Usk/ Afon WysgHorticulture900to1200FreeDrain | 0.16 | 9.94
River Usk/ Afon Wysg | Horticulture | Garddwriaeth | 900to1200 | DrainedAr | River Usk/ Afon WysgHorticulture900to1200DrainedAr | 0.48 | 8.98
River Usk/ Afon Wysg | Horticulture | Garddwriaeth | 900to1200 | DrainedArGr | River Usk/ Afon WysgHorticulture900to1200DrainedArGr | 0.83 | 7.36
River Usk/ Afon Wysg | Horticulture | Garddwriaeth | 1200to1500 | FreeDrain | River Usk/ Afon WysgHorticulture1200to1500FreeDrain | 0.25 | 10.6
River Usk/ Afon Wysg | Horticulture | Garddwriaeth | 1200to1500 | DrainedAr | River Usk/ Afon WysgHorticulture1200to1500DrainedAr | 0.78 | 11.17
River Usk/ Afon Wysg | Horticulture | Garddwriaeth | 1200to1500 | DrainedArGr | River Usk/ Afon WysgHorticulture1200to1500DrainedArGr | 1.26 | 9.53
River Usk/ Afon Wysg | Horticulture | Garddwriaeth | Over1500 | FreeDrain | River Usk/ Afon WysgHorticultureOver1500FreeDrain | 0.44 | 10.75
River Usk/ Afon Wysg | Horticulture | Garddwriaeth | Over1500 | DrainedAr | River Usk/ Afon WysgHorticultureOver1500DrainedAr | 1.07 | 13.07
River Usk/ Afon Wysg | Horticulture | Garddwriaeth | Over1500 | DrainedArGr | River Usk/ Afon WysgHorticultureOver1500DrainedArGr | 2.23 | 12.16
River Usk/ Afon Wysg | Indoor pig farming | Ffermio moch dan do | 900to1200 | FreeDrain | River Usk/ Afon WysgIndoor pig farming900to1200FreeDrain | 0.28 | 29.58
River Usk/ Afon Wysg | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedAr | River Usk/ Afon WysgIndoor pig farming900to1200DrainedAr | 1.1 | 26.27
River Usk/ Afon Wysg | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedArGr | River Usk/ Afon WysgIndoor pig farming900to1200DrainedArGr | 1.43 | 21.02
River Usk/ Afon Wysg | Indoor pig farming | Ffermio moch dan do | 1200to1500 | FreeDrain | River Usk/ Afon WysgIndoor pig farming1200to1500FreeDrain | 0.43 | 30.49
River Usk/ Afon Wysg | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedAr | River Usk/ Afon WysgIndoor pig farming1200to1500DrainedAr | 1.78 | 31.56
River Usk/ Afon Wysg | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedArGr | River Usk/ Afon WysgIndoor pig farming1200to1500DrainedArGr | 2.07 | 24.89
River Usk/ Afon Wysg | Indoor pig farming | Ffermio moch dan do | Over1500 | FreeDrain | River Usk/ Afon WysgIndoor pig farmingOver1500FreeDrain | 0.78 | 31.67
River Usk/ Afon Wysg | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedAr | River Usk/ Afon WysgIndoor pig farmingOver1500DrainedAr | 2.4 | 37.47
River Usk/ Afon Wysg | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedArGr | River Usk/ Afon WysgIndoor pig farmingOver1500DrainedArGr | 3.87 | 30.72
River Usk/ Afon Wysg | Poultry | Dofednod | 900to1200 | FreeDrain | River Usk/ Afon WysgPoultry900to1200FreeDrain | 0.22 | 60.13
River Usk/ Afon Wysg | Poultry | Dofednod | 900to1200 | DrainedAr | River Usk/ Afon WysgPoultry900to1200DrainedAr | 0.49 | 50.41
River Usk/ Afon Wysg | Poultry | Dofednod | 900to1200 | DrainedArGr | River Usk/ Afon WysgPoultry900to1200DrainedArGr | 1.26 | 35.56
River Usk/ Afon Wysg | Poultry | Dofednod | 1200to1500 | FreeDrain | River Usk/ Afon WysgPoultry1200to1500FreeDrain | 0.31 | 61.03
River Usk/ Afon Wysg | Poultry | Dofednod | 1200to1500 | DrainedAr | River Usk/ Afon WysgPoultry1200to1500DrainedAr | 0.76 | 57.17
River Usk/ Afon Wysg | Poultry | Dofednod | 1200to1500 | DrainedArGr | River Usk/ Afon WysgPoultry1200to1500DrainedArGr | 1.81 | 41.02
River Usk/ Afon Wysg | Poultry | Dofednod | Over1500 | FreeDrain | River Usk/ Afon WysgPoultryOver1500FreeDrain | 0.51 | 61.74
River Usk/ Afon Wysg | Poultry | Dofednod | Over1500 | DrainedAr | River Usk/ Afon WysgPoultryOver1500DrainedAr | 1.02 | 65.07
River Usk/ Afon Wysg | Poultry | Dofednod | Over1500 | DrainedArGr | River Usk/ Afon WysgPoultryOver1500DrainedArGr | 2.86 | 47.76
River Usk/ Afon Wysg | Dairy | Llaeth | 900to1200 | FreeDrain | River Usk/ Afon WysgDairy900to1200FreeDrain | 0.18 | 13.65
River Usk/ Afon Wysg | Dairy | Llaeth | 900to1200 | DrainedAr | River Usk/ Afon WysgDairy900to1200DrainedAr | 0.26 | 12.92
River Usk/ Afon Wysg | Dairy | Llaeth | 900to1200 | DrainedArGr | River Usk/ Afon WysgDairy900to1200DrainedArGr | 1.08 | 12.29
River Usk/ Afon Wysg | Dairy | Llaeth | 1200to1500 | FreeDrain | River Usk/ Afon WysgDairy1200to1500FreeDrain | 0.25 | 13.55
River Usk/ Afon Wysg | Dairy | Llaeth | 1200to1500 | DrainedAr | River Usk/ Afon WysgDairy1200to1500DrainedAr | 0.41 | 14.96
River Usk/ Afon Wysg | Dairy | Llaeth | 1200to1500 | DrainedArGr | River Usk/ Afon WysgDairy1200to1500DrainedArGr | 1.6 | 16.54
River Usk/ Afon Wysg | Dairy | Llaeth | Over1500 | FreeDrain | River Usk/ Afon WysgDairyOver1500FreeDrain | 0.39 | 12.96
River Usk/ Afon Wysg | Dairy | Llaeth | Over1500 | DrainedAr | River Usk/ Afon WysgDairyOver1500DrainedAr | 0.54 | 16.99
River Usk/ Afon Wysg | Dairy | Llaeth | Over1500 | DrainedArGr | River Usk/ Afon WysgDairyOver1500DrainedArGr | 2.45 | 23.13
River Usk/ Afon Wysg | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | FreeDrain | River Usk/ Afon WysgLess Favoured Area grazing900to1200FreeDrain | 0.19 | 14.78
River Usk/ Afon Wysg | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedAr | River Usk/ Afon WysgLess Favoured Area grazing900to1200DrainedAr | 0.2 | 14.21
River Usk/ Afon Wysg | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedArGr | River Usk/ Afon WysgLess Favoured Area grazing900to1200DrainedArGr | 1.18 | 13.28
River Usk/ Afon Wysg | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | FreeDrain | River Usk/ Afon WysgLess Favoured Area grazing1200to1500FreeDrain | 0.26 | 14.5
River Usk/ Afon Wysg | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedAr | River Usk/ Afon WysgLess Favoured Area grazing1200to1500DrainedAr | 0.32 | 16.04
River Usk/ Afon Wysg | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedArGr | River Usk/ Afon WysgLess Favoured Area grazing1200to1500DrainedArGr | 1.68 | 16.45
River Usk/ Afon Wysg | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | FreeDrain | River Usk/ Afon WysgLess Favoured Area grazingOver1500FreeDrain | 0.39 | 13.47
River Usk/ Afon Wysg | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedAr | River Usk/ Afon WysgLess Favoured Area grazingOver1500DrainedAr | 0.4 | 17.46
River Usk/ Afon Wysg | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedArGr | River Usk/ Afon WysgLess Favoured Area grazingOver1500DrainedArGr | 2.4 | 20.44
River Usk/ Afon Wysg | Lowland grazing | Pori iseldir | 900to1200 | FreeDrain | River Usk/ Afon WysgLowland grazing900to1200FreeDrain | 0.21 | 18.01
River Usk/ Afon Wysg | Lowland grazing | Pori iseldir | 900to1200 | DrainedAr | River Usk/ Afon WysgLowland grazing900to1200DrainedAr | 0.27 | 17.12
River Usk/ Afon Wysg | Lowland grazing | Pori iseldir | 900to1200 | DrainedArGr | River Usk/ Afon WysgLowland grazing900to1200DrainedArGr | 1.37 | 15.19
River Usk/ Afon Wysg | Lowland grazing | Pori iseldir | 1200to1500 | FreeDrain | River Usk/ Afon WysgLowland grazing1200to1500FreeDrain | 0.29 | 17.74
River Usk/ Afon Wysg | Lowland grazing | Pori iseldir | 1200to1500 | DrainedAr | River Usk/ Afon WysgLowland grazing1200to1500DrainedAr | 0.43 | 19.49
River Usk/ Afon Wysg | Lowland grazing | Pori iseldir | 1200to1500 | DrainedArGr | River Usk/ Afon WysgLowland grazing1200to1500DrainedArGr | 1.95 | 19.06
River Usk/ Afon Wysg | Lowland grazing | Pori iseldir | Over1500 | FreeDrain | River Usk/ Afon WysgLowland grazingOver1500FreeDrain | 0.44 | 16.48
River Usk/ Afon Wysg | Lowland grazing | Pori iseldir | Over1500 | DrainedAr | River Usk/ Afon WysgLowland grazingOver1500DrainedAr | 0.54 | 21.51
River Usk/ Afon Wysg | Lowland grazing | Pori iseldir | Over1500 | DrainedArGr | River Usk/ Afon WysgLowland grazingOver1500DrainedArGr | 2.82 | 23.88
River Usk/ Afon Wysg | Mixed | Cymysg | 900to1200 | FreeDrain | River Usk/ Afon WysgMixed900to1200FreeDrain | 0.22 | 19.88
River Usk/ Afon Wysg | Mixed | Cymysg | 900to1200 | DrainedAr | River Usk/ Afon WysgMixed900to1200DrainedAr | 0.44 | 18.81
River Usk/ Afon Wysg | Mixed | Cymysg | 900to1200 | DrainedArGr | River Usk/ Afon WysgMixed900to1200DrainedArGr | 1.45 | 16.6
River Usk/ Afon Wysg | Mixed | Cymysg | 1200to1500 | FreeDrain | River Usk/ Afon WysgMixed1200to1500FreeDrain | 0.31 | 19.76
River Usk/ Afon Wysg | Mixed | Cymysg | 1200to1500 | DrainedAr | River Usk/ Afon WysgMixed1200to1500DrainedAr | 0.7 | 21.77
River Usk/ Afon Wysg | Mixed | Cymysg | 1200to1500 | DrainedArGr | River Usk/ Afon WysgMixed1200to1500DrainedArGr | 2.05 | 20.81
River Usk/ Afon Wysg | Mixed | Cymysg | Over1500 | FreeDrain | River Usk/ Afon WysgMixedOver1500FreeDrain | 0.49 | 18.76
River Usk/ Afon Wysg | Mixed | Cymysg | Over1500 | DrainedAr | River Usk/ Afon WysgMixedOver1500DrainedAr | 0.91 | 24.47
River Usk/ Afon Wysg | Mixed | Cymysg | Over1500 | DrainedArGr | River Usk/ Afon WysgMixedOver1500DrainedArGr | 3.13 | 26.28
River Usk/ Afon Wysg | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | FreeDrain | River Usk/ Afon WysgOutdoor pig farming900to1200FreeDrain | 0.41 | 34.24
River Usk/ Afon Wysg | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedAr | River Usk/ Afon WysgOutdoor pig farming900to1200DrainedAr | 1.99 | 35.4
River Usk/ Afon Wysg | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedArGr | River Usk/ Afon WysgOutdoor pig farming900to1200DrainedArGr | 2.09 | 31.27
River Usk/ Afon Wysg | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | FreeDrain | River Usk/ Afon WysgOutdoor pig farming1200to1500FreeDrain | 0.6 | 35.06
River Usk/ Afon Wysg | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedAr | River Usk/ Afon WysgOutdoor pig farming1200to1500DrainedAr | 3.18 | 43.87
River Usk/ Afon Wysg | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedArGr | River Usk/ Afon WysgOutdoor pig farming1200to1500DrainedArGr | 2.97 | 38.04
River Usk/ Afon Wysg | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | FreeDrain | River Usk/ Afon WysgOutdoor pig farmingOver1500FreeDrain | 1.13 | 37.52
River Usk/ Afon Wysg | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedAr | River Usk/ Afon WysgOutdoor pig farmingOver1500DrainedAr | 4.19 | 54.24
River Usk/ Afon Wysg | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedArGr | River Usk/ Afon WysgOutdoor pig farmingOver1500DrainedArGr | 5.86 | 49.31
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | 600to700 | FreeDrain | River Wye/ Afon GwyCereals600to700FreeDrain | 0.04 | 9.77
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | 600to700 | DrainedAr | River Wye/ Afon GwyCereals600to700DrainedAr | 0.13 | 7.37
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | 600to700 | DrainedArGr | River Wye/ Afon GwyCereals600to700DrainedArGr | 0.34 | 8.07
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | 700to900 | FreeDrain | River Wye/ Afon GwyCereals700to900FreeDrain | 0.1 | 12.65
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | 700to900 | DrainedAr | River Wye/ Afon GwyCereals700to900DrainedAr | 0.29 | 10.24
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | 700to900 | DrainedArGr | River Wye/ Afon GwyCereals700to900DrainedArGr | 0.58 | 9.44
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | 900to1200 | FreeDrain | River Wye/ Afon GwyCereals900to1200FreeDrain | 0.18 | 14.06
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | 900to1200 | DrainedAr | River Wye/ Afon GwyCereals900to1200DrainedAr | 0.54 | 13.78
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | 900to1200 | DrainedArGr | River Wye/ Afon GwyCereals900to1200DrainedArGr | 0.98 | 12.11
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | 1200to1500 | FreeDrain | River Wye/ Afon GwyCereals1200to1500FreeDrain | 0.26 | 14.68
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | 1200to1500 | DrainedAr | River Wye/ Afon GwyCereals1200to1500DrainedAr | 0.87 | 16.96
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | 1200to1500 | DrainedArGr | River Wye/ Afon GwyCereals1200to1500DrainedArGr | 1.45 | 15.46
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | Over1500 | FreeDrain | River Wye/ Afon GwyCerealsOver1500FreeDrain | 0.46 | 14.88
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | Over1500 | DrainedAr | River Wye/ Afon GwyCerealsOver1500DrainedAr | 1.16 | 20.01
River Wye/ Afon Gwy | Cereals | Grawnfwydydd | Over1500 | DrainedArGr | River Wye/ Afon GwyCerealsOver1500DrainedArGr | 2.5 | 19.81
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | 600to700 | FreeDrain | River Wye/ Afon GwyGeneral cropping600to700FreeDrain | 0.03 | 5.05
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | 600to700 | DrainedAr | River Wye/ Afon GwyGeneral cropping600to700DrainedAr | 0.08 | 3.57
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | 600to700 | DrainedArGr | River Wye/ Afon GwyGeneral cropping600to700DrainedArGr | 0.24 | 3.35
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | 700to900 | FreeDrain | River Wye/ Afon GwyGeneral cropping700to900FreeDrain | 0.08 | 6.4
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | 700to900 | DrainedAr | River Wye/ Afon GwyGeneral cropping700to900DrainedAr | 0.17 | 4.98
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | 700to900 | DrainedArGr | River Wye/ Afon GwyGeneral cropping700to900DrainedArGr | 0.43 | 4
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | 900to1200 | FreeDrain | River Wye/ Afon GwyGeneral cropping900to1200FreeDrain | 0.14 | 7.14
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | 900to1200 | DrainedAr | River Wye/ Afon GwyGeneral cropping900to1200DrainedAr | 0.32 | 6.63
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | 900to1200 | DrainedArGr | River Wye/ Afon GwyGeneral cropping900to1200DrainedArGr | 0.77 | 5.5
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | 1200to1500 | FreeDrain | River Wye/ Afon GwyGeneral cropping1200to1500FreeDrain | 0.22 | 7.55
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedAr | River Wye/ Afon GwyGeneral cropping1200to1500DrainedAr | 0.53 | 8.16
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | 1200to1500 | DrainedArGr | River Wye/ Afon GwyGeneral cropping1200to1500DrainedArGr | 1.19 | 7.42
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | Over1500 | FreeDrain | River Wye/ Afon GwyGeneral croppingOver1500FreeDrain | 0.37 | 7.51
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | Over1500 | DrainedAr | River Wye/ Afon GwyGeneral croppingOver1500DrainedAr | 0.72 | 9.46
River Wye/ Afon Gwy | General cropping | Cnydio cyffredinol | Over1500 | DrainedArGr | River Wye/ Afon GwyGeneral croppingOver1500DrainedArGr | 2.01 | 9.92
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | 600to700 | FreeDrain | River Wye/ Afon GwyHorticulture600to700FreeDrain | 0.03 | 6.44
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | 600to700 | DrainedAr | River Wye/ Afon GwyHorticulture600to700DrainedAr | 0.1 | 4.55
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | 600to700 | DrainedArGr | River Wye/ Afon GwyHorticulture600to700DrainedArGr | 0.26 | 4.42
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | 700to900 | FreeDrain | River Wye/ Afon GwyHorticulture700to900FreeDrain | 0.09 | 8
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | 700to900 | DrainedAr | River Wye/ Afon GwyHorticulture700to900DrainedAr | 0.22 | 6.09
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | 700to900 | DrainedArGr | River Wye/ Afon GwyHorticulture700to900DrainedArGr | 0.46 | 5.09
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | 900to1200 | FreeDrain | River Wye/ Afon GwyHorticulture900to1200FreeDrain | 0.16 | 8.97
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | 900to1200 | DrainedAr | River Wye/ Afon GwyHorticulture900to1200DrainedAr | 0.43 | 8.11
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | 900to1200 | DrainedArGr | River Wye/ Afon GwyHorticulture900to1200DrainedArGr | 0.82 | 6.69
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | 1200to1500 | FreeDrain | River Wye/ Afon GwyHorticulture1200to1500FreeDrain | 0.24 | 9.54
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | 1200to1500 | DrainedAr | River Wye/ Afon GwyHorticulture1200to1500DrainedAr | 0.71 | 10.06
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | 1200to1500 | DrainedArGr | River Wye/ Afon GwyHorticulture1200to1500DrainedArGr | 1.24 | 8.76
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | Over1500 | FreeDrain | River Wye/ Afon GwyHorticultureOver1500FreeDrain | 0.42 | 9.62
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | Over1500 | DrainedAr | River Wye/ Afon GwyHorticultureOver1500DrainedAr | 0.96 | 11.72
River Wye/ Afon Gwy | Horticulture | Garddwriaeth | Over1500 | DrainedArGr | River Wye/ Afon GwyHorticultureOver1500DrainedArGr | 2.17 | 11.33
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | 600to700 | FreeDrain | River Wye/ Afon GwyIndoor pig farming600to700FreeDrain | 0.07 | 42.28
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | 600to700 | DrainedAr | River Wye/ Afon GwyIndoor pig farming600to700DrainedAr | 0.27 | 29.4
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | 600to700 | DrainedArGr | River Wye/ Afon GwyIndoor pig farming600to700DrainedArGr | 0.81 | 27.8
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | 700to900 | FreeDrain | River Wye/ Afon GwyIndoor pig farming700to900FreeDrain | 0.18 | 51.48
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | 700to900 | DrainedAr | River Wye/ Afon GwyIndoor pig farming700to900DrainedAr | 0.56 | 38.37
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | 700to900 | DrainedArGr | River Wye/ Afon GwyIndoor pig farming700to900DrainedArGr | 1.2 | 30.63
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | 900to1200 | FreeDrain | River Wye/ Afon GwyIndoor pig farming900to1200FreeDrain | 0.3 | 54.83
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedAr | River Wye/ Afon GwyIndoor pig farming900to1200DrainedAr | 1.03 | 47.33
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | 900to1200 | DrainedArGr | River Wye/ Afon GwyIndoor pig farming900to1200DrainedArGr | 1.81 | 34.95
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | 1200to1500 | FreeDrain | River Wye/ Afon GwyIndoor pig farming1200to1500FreeDrain | 0.44 | 56.41
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedAr | River Wye/ Afon GwyIndoor pig farming1200to1500DrainedAr | 1.64 | 55.14
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | 1200to1500 | DrainedArGr | River Wye/ Afon GwyIndoor pig farming1200to1500DrainedArGr | 2.49 | 40.43
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | Over1500 | FreeDrain | River Wye/ Afon GwyIndoor pig farmingOver1500FreeDrain | 0.78 | 58.28
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedAr | River Wye/ Afon GwyIndoor pig farmingOver1500DrainedAr | 2.19 | 64.45
River Wye/ Afon Gwy | Indoor pig farming | Ffermio moch dan do | Over1500 | DrainedArGr | River Wye/ Afon GwyIndoor pig farmingOver1500DrainedArGr | 4.2 | 48.22
River Wye/ Afon Gwy | Poultry | Dofednod | 600to700 | FreeDrain | River Wye/ Afon GwyPoultry600to700FreeDrain | 0.07 | 40.39
River Wye/ Afon Gwy | Poultry | Dofednod | 600to700 | DrainedAr | River Wye/ Afon GwyPoultry600to700DrainedAr | 0.13 | 27.45
River Wye/ Afon Gwy | Poultry | Dofednod | 600to700 | DrainedArGr | River Wye/ Afon GwyPoultry600to700DrainedArGr | 0.58 | 23.49
River Wye/ Afon Gwy | Poultry | Dofednod | 700to900 | FreeDrain | River Wye/ Afon GwyPoultry700to900FreeDrain | 0.14 | 49.9
River Wye/ Afon Gwy | Poultry | Dofednod | 700to900 | DrainedAr | River Wye/ Afon GwyPoultry700to900DrainedAr | 0.25 | 36.92
River Wye/ Afon Gwy | Poultry | Dofednod | 700to900 | DrainedArGr | River Wye/ Afon GwyPoultry700to900DrainedArGr | 0.86 | 26.49
River Wye/ Afon Gwy | Poultry | Dofednod | 900to1200 | FreeDrain | River Wye/ Afon GwyPoultry900to1200FreeDrain | 0.22 | 52.58
River Wye/ Afon Gwy | Poultry | Dofednod | 900to1200 | DrainedAr | River Wye/ Afon GwyPoultry900to1200DrainedAr | 0.43 | 44.84
River Wye/ Afon Gwy | Poultry | Dofednod | 900to1200 | DrainedArGr | River Wye/ Afon GwyPoultry900to1200DrainedArGr | 1.37 | 30.58
River Wye/ Afon Gwy | Poultry | Dofednod | 1200to1500 | FreeDrain | River Wye/ Afon GwyPoultry1200to1500FreeDrain | 0.31 | 52.99
River Wye/ Afon Gwy | Poultry | Dofednod | 1200to1500 | DrainedAr | River Wye/ Afon GwyPoultry1200to1500DrainedAr | 0.66 | 50.52
River Wye/ Afon Gwy | Poultry | Dofednod | 1200to1500 | DrainedArGr | River Wye/ Afon GwyPoultry1200to1500DrainedArGr | 1.94 | 35.78
River Wye/ Afon Gwy | Poultry | Dofednod | Over1500 | FreeDrain | River Wye/ Afon GwyPoultryOver1500FreeDrain | 0.5 | 52.71
River Wye/ Afon Gwy | Poultry | Dofednod | Over1500 | DrainedAr | River Wye/ Afon GwyPoultryOver1500DrainedAr | 0.88 | 57.43
River Wye/ Afon Gwy | Poultry | Dofednod | Over1500 | DrainedArGr | River Wye/ Afon GwyPoultryOver1500DrainedArGr | 2.96 | 42.25
River Wye/ Afon Gwy | Dairy | Llaeth | 600to700 | FreeDrain | River Wye/ Afon GwyDairy600to700FreeDrain | 0.06 | 7.88
River Wye/ Afon Gwy | Dairy | Llaeth | 600to700 | DrainedAr | River Wye/ Afon GwyDairy600to700DrainedAr | 0.07 | 5.49
River Wye/ Afon Gwy | Dairy | Llaeth | 600to700 | DrainedArGr | River Wye/ Afon GwyDairy600to700DrainedArGr | 0.37 | 6.08
River Wye/ Afon Gwy | Dairy | Llaeth | 700to900 | FreeDrain | River Wye/ Afon GwyDairy700to900FreeDrain | 0.1 | 11.03
River Wye/ Afon Gwy | Dairy | Llaeth | 700to900 | DrainedAr | River Wye/ Afon GwyDairy700to900DrainedAr | 0.13 | 8.78
River Wye/ Afon Gwy | Dairy | Llaeth | 700to900 | DrainedArGr | River Wye/ Afon GwyDairy700to900DrainedArGr | 0.6 | 7.98
River Wye/ Afon Gwy | Dairy | Llaeth | 900to1200 | FreeDrain | River Wye/ Afon GwyDairy900to1200FreeDrain | 0.17 | 11.85
River Wye/ Afon Gwy | Dairy | Llaeth | 900to1200 | DrainedAr | River Wye/ Afon GwyDairy900to1200DrainedAr | 0.23 | 11.28
River Wye/ Afon Gwy | Dairy | Llaeth | 900to1200 | DrainedArGr | River Wye/ Afon GwyDairy900to1200DrainedArGr | 1.03 | 11.56
River Wye/ Afon Gwy | Dairy | Llaeth | 1200to1500 | FreeDrain | River Wye/ Afon GwyDairy1200to1500FreeDrain | 0.24 | 11.78
River Wye/ Afon Gwy | Dairy | Llaeth | 1200to1500 | DrainedAr | River Wye/ Afon GwyDairy1200to1500DrainedAr | 0.37 | 13.12
River Wye/ Afon Gwy | Dairy | Llaeth | 1200to1500 | DrainedArGr | River Wye/ Afon GwyDairy1200to1500DrainedArGr | 1.53 | 15.66
River Wye/ Afon Gwy | Dairy | Llaeth | Over1500 | FreeDrain | River Wye/ Afon GwyDairyOver1500FreeDrain | 0.37 | 11.33
River Wye/ Afon Gwy | Dairy | Llaeth | Over1500 | DrainedAr | River Wye/ Afon GwyDairyOver1500DrainedAr | 0.48 | 14.85
River Wye/ Afon Gwy | Dairy | Llaeth | Over1500 | DrainedArGr | River Wye/ Afon GwyDairyOver1500DrainedArGr | 2.33 | 22.06
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 600to700 | FreeDrain | River Wye/ Afon GwyLess Favoured Area grazing600to700FreeDrain | 0.07 | 9.05
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 600to700 | DrainedAr | River Wye/ Afon GwyLess Favoured Area grazing600to700DrainedAr | 0.08 | 6.56
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 600to700 | DrainedArGr | River Wye/ Afon GwyLess Favoured Area grazing600to700DrainedArGr | 0.45 | 8.11
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 700to900 | FreeDrain | River Wye/ Afon GwyLess Favoured Area grazing700to900FreeDrain | 0.12 | 13.45
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 700to900 | DrainedAr | River Wye/ Afon GwyLess Favoured Area grazing700to900DrainedAr | 0.12 | 10.97
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 700to900 | DrainedArGr | River Wye/ Afon GwyLess Favoured Area grazing700to900DrainedArGr | 0.65 | 10.46
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | FreeDrain | River Wye/ Afon GwyLess Favoured Area grazing900to1200FreeDrain | 0.18 | 14.69
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedAr | River Wye/ Afon GwyLess Favoured Area grazing900to1200DrainedAr | 0.19 | 14.19
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 900to1200 | DrainedArGr | River Wye/ Afon GwyLess Favoured Area grazing900to1200DrainedArGr | 1.02 | 13.53
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | FreeDrain | River Wye/ Afon GwyLess Favoured Area grazing1200to1500FreeDrain | 0.25 | 14.45
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedAr | River Wye/ Afon GwyLess Favoured Area grazing1200to1500DrainedAr | 0.3 | 15.88
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | 1200to1500 | DrainedArGr | River Wye/ Afon GwyLess Favoured Area grazing1200to1500DrainedArGr | 1.44 | 16.34
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | FreeDrain | River Wye/ Afon GwyLess Favoured Area grazingOver1500FreeDrain | 0.39 | 13.6
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedAr | River Wye/ Afon GwyLess Favoured Area grazingOver1500DrainedAr | 0.39 | 17.12
River Wye/ Afon Gwy | Less Favoured Area grazing | Pori Ardal Lai Ffafriol | Over1500 | DrainedArGr | River Wye/ Afon GwyLess Favoured Area grazingOver1500DrainedArGr | 2.06 | 19.88
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | 600to700 | FreeDrain | River Wye/ Afon GwyLowland grazing600to700FreeDrain | 0.09 | 11.96
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | 600to700 | DrainedAr | River Wye/ Afon GwyLowland grazing600to700DrainedAr | 0.11 | 8.29
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | 600to700 | DrainedArGr | River Wye/ Afon GwyLowland grazing600to700DrainedArGr | 0.63 | 10.17
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | 700to900 | FreeDrain | River Wye/ Afon GwyLowland grazing700to900FreeDrain | 0.15 | 17.94
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | 700to900 | DrainedAr | River Wye/ Afon GwyLowland grazing700to900DrainedAr | 0.17 | 14.18
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | 700to900 | DrainedArGr | River Wye/ Afon GwyLowland grazing700to900DrainedArGr | 0.91 | 12.83
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | 900to1200 | FreeDrain | River Wye/ Afon GwyLowland grazing900to1200FreeDrain | 0.22 | 19.61
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | 900to1200 | DrainedAr | River Wye/ Afon GwyLowland grazing900to1200DrainedAr | 0.27 | 18.72
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | 900to1200 | DrainedArGr | River Wye/ Afon GwyLowland grazing900to1200DrainedArGr | 1.43 | 17.06
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | 1200to1500 | FreeDrain | River Wye/ Afon GwyLowland grazing1200to1500FreeDrain | 0.3 | 19.28
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | 1200to1500 | DrainedAr | River Wye/ Afon GwyLowland grazing1200to1500DrainedAr | 0.42 | 21.25
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | 1200to1500 | DrainedArGr | River Wye/ Afon GwyLowland grazing1200to1500DrainedArGr | 2 | 21.22
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | Over1500 | FreeDrain | River Wye/ Afon GwyLowland grazingOver1500FreeDrain | 0.45 | 17.93
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | Over1500 | DrainedAr | River Wye/ Afon GwyLowland grazingOver1500DrainedAr | 0.54 | 23.34
River Wye/ Afon Gwy | Lowland grazing | Pori iseldir | Over1500 | DrainedArGr | River Wye/ Afon GwyLowland grazingOver1500DrainedArGr | 2.86 | 26.38
River Wye/ Afon Gwy | Mixed | Cymysg | 600to700 | FreeDrain | River Wye/ Afon GwyMixed600to700FreeDrain | 0.08 | 13.2
River Wye/ Afon Gwy | Mixed | Cymysg | 600to700 | DrainedAr | River Wye/ Afon GwyMixed600to700DrainedAr | 0.13 | 9.23
River Wye/ Afon Gwy | Mixed | Cymysg | 600to700 | DrainedArGr | River Wye/ Afon GwyMixed600to700DrainedArGr | 0.63 | 10.95
River Wye/ Afon Gwy | Mixed | Cymysg | 700to900 | FreeDrain | River Wye/ Afon GwyMixed700to900FreeDrain | 0.14 | 19.04
River Wye/ Afon Gwy | Mixed | Cymysg | 700to900 | DrainedAr | River Wye/ Afon GwyMixed700to900DrainedAr | 0.23 | 14.99
River Wye/ Afon Gwy | Mixed | Cymysg | 700to900 | DrainedArGr | River Wye/ Afon GwyMixed700to900DrainedArGr | 0.94 | 13.55
River Wye/ Afon Gwy | Mixed | Cymysg | 900to1200 | FreeDrain | River Wye/ Afon GwyMixed900to1200FreeDrain | 0.22 | 20.75
River Wye/ Afon Gwy | Mixed | Cymysg | 900to1200 | DrainedAr | River Wye/ Afon GwyMixed900to1200DrainedAr | 0.39 | 19.69
River Wye/ Afon Gwy | Mixed | Cymysg | 900to1200 | DrainedArGr | River Wye/ Afon GwyMixed900to1200DrainedArGr | 1.47 | 17.85
River Wye/ Afon Gwy | Mixed | Cymysg | 1200to1500 | FreeDrain | River Wye/ Afon GwyMixed1200to1500FreeDrain | 0.3 | 20.54
River Wye/ Afon Gwy | Mixed | Cymysg | 1200to1500 | DrainedAr | River Wye/ Afon GwyMixed1200to1500DrainedAr | 0.62 | 22.64
River Wye/ Afon Gwy | Mixed | Cymysg | 1200to1500 | DrainedArGr | River Wye/ Afon GwyMixed1200to1500DrainedArGr | 2.07 | 22.27
River Wye/ Afon Gwy | Mixed | Cymysg | Over1500 | FreeDrain | River Wye/ Afon GwyMixedOver1500FreeDrain | 0.48 | 19.4
River Wye/ Afon Gwy | Mixed | Cymysg | Over1500 | DrainedAr | River Wye/ Afon GwyMixedOver1500DrainedAr | 0.8 | 25.21
River Wye/ Afon Gwy | Mixed | Cymysg | Over1500 | DrainedArGr | River Wye/ Afon GwyMixedOver1500DrainedArGr | 3.09 | 27.96
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | 600to700 | FreeDrain | River Wye/ Afon GwyOutdoor pig farming600to700FreeDrain | 0.07 | 26.56
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | 600to700 | DrainedAr | River Wye/ Afon GwyOutdoor pig farming600to700DrainedAr | 0.45 | 21.55
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | 600to700 | DrainedArGr | River Wye/ Afon GwyOutdoor pig farming600to700DrainedArGr | 0.7 | 23.66
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | 700to900 | FreeDrain | River Wye/ Afon GwyOutdoor pig farming700to900FreeDrain | 0.24 | 32.04
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | 700to900 | DrainedAr | River Wye/ Afon GwyOutdoor pig farming700to900DrainedAr | 1.05 | 27.14
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | 700to900 | DrainedArGr | River Wye/ Afon GwyOutdoor pig farming700to900DrainedArGr | 1.28 | 26.5
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | FreeDrain | River Wye/ Afon GwyOutdoor pig farming900to1200FreeDrain | 0.41 | 34.13
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedAr | River Wye/ Afon GwyOutdoor pig farming900to1200DrainedAr | 1.99 | 35.27
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | 900to1200 | DrainedArGr | River Wye/ Afon GwyOutdoor pig farming900to1200DrainedArGr | 2.09 | 31.14
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | FreeDrain | River Wye/ Afon GwyOutdoor pig farming1200to1500FreeDrain | 0.6 | 34.94
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedAr | River Wye/ Afon GwyOutdoor pig farming1200to1500DrainedAr | 3.19 | 43.7
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | 1200to1500 | DrainedArGr | River Wye/ Afon GwyOutdoor pig farming1200to1500DrainedArGr | 2.98 | 37.88
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | FreeDrain | River Wye/ Afon GwyOutdoor pig farmingOver1500FreeDrain | 1.13 | 37.39
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedAr | River Wye/ Afon GwyOutdoor pig farmingOver1500DrainedAr | 4.2 | 54.02
River Wye/ Afon Gwy | Outdoor pig farming | Ffermio moch yn yr awyr agored | Over1500 | DrainedArGr | River Wye/ Afon GwyOutdoor pig farmingOver1500DrainedArGr | 5.88 | 49.1
All | Greenspace | Mannau gwyrdd | - | - | Greenspace | 0.02 | 3
All | Community food growing | Tyfu bwyd cymunedol | - | - | Community food growing | 0.09 | 6.9
All | Woodland | Coetir | - | - | Woodland | 0.02 | 3
All | Shrub | Llwyn | - | - | Shrub | 0.02 | 3
All | Water | Dwfr | - | - | Water | 0 | 0
All | Residential land | Tir preswyl | - | - | Residential land | 1.58 | 14.74
All | Commercial/industrial land | Tir masnachol/diwydiannol | - | - | Commercial/industrial land | 1.16 | 7.86
All | Open land – built environment | Tir agored – amgylchedd adeiledig | - | - | Open land – built environment | 0.85 | 8.69
Table 5: Stage 2 and 3 rainfall and urban export coefficient lookup
Rainfall band | Mid | Farmscoper Equivalent | P Urban Runoff Coefficient | N Urban Runoff Coefficient | Residential P export coefficient (kg/ha/yr) | Commercial / industrial P export coefficient (kg/ha/yr) | Open urban P export coefficient (kg/ha/yr) | Residential N export coefficient (kg/ha/yr) | Commercial / industrial N export coefficient (kg/ha/yr) | Open urban N export coefficient (kg/ha/yr)
508 - 525 | 516.5 | Under600 | 47.3663 | 63.9463 | 1.0031 | 0.73394 | 0.53822 | 9.4131 | 5.0203 | 5.5488
525.1 - 550 | 537.55 | Under600 | 47.6055 | 64.1855 | 1.0492 | 0.76771 | 0.56299 | 9.8333 | 5.2444 | 5.7965
550.1 - 575 | 562.55 | Under600 | 47.8625 | 64.4425 | 1.1039 | 0.80775 | 0.59235 | 10.3319 | 5.5103 | 6.0904
575.1 - 600 | 587.55 | Under600 | 48.0897 | 64.6697 | 1.1585 | 0.84765 | 0.62161 | 10.8291 | 5.7755 | 6.3834
600.1 - 625 | 612.55 | 600to700 | 48.2869 | 64.8669 | 1.2127 | 0.88734 | 0.65072 | 11.3243 | 6.0396 | 6.6753
625.1 - 650 | 637.55 | 600to700 | 48.4537 | 65.0337 | 1.2666 | 0.92675 | 0.67962 | 11.8167 | 6.3023 | 6.9657
650.1 - 675 | 662.55 | 600to700 | 48.5897 | 65.1697 | 1.3199 | 0.96579 | 0.70825 | 12.3058 | 6.5631 | 7.2539
675.1 - 700 | 687.55 | 600to700 | 48.6947 | 65.2747 | 1.3727 | 1.0044 | 0.73656 | 12.7907 | 6.8217 | 7.5398
700.1 - 750 | 725.05 | 700to900 | 48.7932 | 65.3732 | 1.4505 | 1.0613 | 0.7783 | 13.5087 | 7.2046 | 7.963
750.1 - 800 | 775.05 | 700to900 | 48.818 | 65.398 | 1.5513 | 1.1351 | 0.8324 | 14.4457 | 7.7044 | 8.5154
800.1 - 850 | 825.05 | 700to900 | 48.818 | 65.398 | 1.6514 | 1.2083 | 0.8861 | 15.3776 | 8.2014 | 9.0647
850.1 - 900 | 875.05 | 700to900 | 48.818 | 65.398 | 1.7514 | 1.2815 | 0.9398 | 16.3096 | 8.6984 | 9.6141
900.1 - 950 | 925.05 | 900to1200 | 48.818 | 65.398 | 1.8515 | 1.3548 | 0.9935 | 17.2415 | 9.1955 | 10.1634
950.1 - 1,000 | 975.05 | 900to1200 | 48.818 | 65.398 | 1.9516 | 1.428 | 1.0472 | 18.1734 | 9.6925 | 10.7127
1,000.1 - 1,100 | 1050.05 | 900to1200 | 48.818 | 65.398 | 2.1017 | 1.5378 | 1.1277 | 19.5713 | 10.438 | 11.5368
1,100.1 - 1,200 | 1150.05 | 900to1200 | 48.818 | 65.398 | 2.3019 | 1.6843 | 1.2351 | 21.4351 | 11.4321 | 12.6354
1,200.1 - 1,400 | 1300.05 | 1200to1500 | 48.818 | 65.398 | 2.6021 | 1.904 | 1.3962 | 24.2309 | 12.9231 | 14.2835
1,400.1 - 1,600 | 1500.05 | 1200to1500 | 48.818 | 65.398 | 3.0024 | 2.1969 | 1.611 | 27.9586 | 14.9112 | 16.4808
1,600.1 - 2,000 | 1800.05 | Over1500 | 48.818 | 65.398 | 3.6029 | 2.6362 | 1.9332 | 33.5501 | 17.8934 | 19.7769
2,000.1 - 2,400 | 2200.05 | Over1500 | 48.818 | 65.398 | 4.4035 | 3.2221 | 2.3628 | 41.0055 | 21.8696 | 24.1717
2,400.1 - 3,000 | 2700.05 | Over1500 | 48.818 | 65.398 | 5.4043 | 3.9543 | 2.8998 | 50.3247 | 26.8398 | 29.6651
3,000.1 - 4,000 | 3500.05 | Over1500 | 48.818 | 65.398 | 7.0055 | 5.126 | 3.759 | 65.2354 | 34.7922 | 38.4546
4,000.1 - 5,500 | 4750.05 | Over1500 | 48.818 | 65.398 | 9.5074 | 6.9566 | 5.1015 | 88.5335 | 47.2179 | 52.1882
Table 6: Rainfall dropdown
SAC | Min | Max | Min band | Max band | Min address | Max adress | Array address | Dynamic Lookup
Afon Eden - Cors Goch Trawsfynydd | 1689 | 2535 | 1,600.1 - 2,000 | 2,400.1 - 3,000 | $A$1432 | $A$1434 | $A$1432:$A$1434 | 650.1 - 675
Afon Gwyrfai a Llyn Cwellyn | 996 | 3416 | 950.1 - 1,000 | 3,000.1 - 4,000 | $A$1427 | $A$1435 | $A$1427:$A$1435 | 675.1 - 700
Afon Teifi/ River Teifi | 898 | 1890 | 850.1 - 900 | 1,600.1 - 2,000 | $A$1425 | $A$1432 | $A$1425:$A$1432 | 700.1 - 750
Afon Tywi/ River Tywi | 1244 | 2895 | 1,200.1 - 1,400 | 2,400.1 - 3,000 | $A$1430 | $A$1434 | $A$1430:$A$1434 | 750.1 - 800
Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | 1133 | 2067 | 1,100.1 - 1,200 | 2,000.1 - 2,400 | $A$1429 | $A$1433 | $A$1429:$A$1433 | 800.1 - 850
Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | 1274 | 4201 | 1,200.1 - 1,400 | 4,000.1 - 5,500 | $A$1430 | $A$1436 | $A$1430:$A$1436 | 850.1 - 900
River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | 664 | 2748 | 650.1 - 675 | 2,400.1 - 3,000 | $A$1420 | $A$1434 | $A$1420:$A$1434 | 900.1 - 950
River Usk/ Afon Wysg | 903 | 2658 | 900.1 - 950 | 2,400.1 - 3,000 | $A$1426 | $A$1434 | $A$1426:$A$1434 | 950.1 - 1,000
River Wye/ Afon Gwy | 665 | 3030 | 650.1 - 675 | 2,400.1 - 3,000 | $A$1420 | $A$1434 | $A$1420:$A$1434 | 1,000.1 - 1,100
Bae ac Aberoedd Caerfyrddin/ Carmarthen Bay and Estuaries | 1270 | 1951 | 1,200.1 - 1,400 | 1,600.1 - 2,000 | $A$1430 | $A$1432 | $A$1430:$A$1432 | 1,100.1 - 1,200
1,200.1 - 1,400
1,400.1 - 1,600
Table 7: Language lookup | [7 empty] | 1,600.1 - 2,000
Title | Language Option | [6 empty] | 2,000.1 - 2,400
Language: | English | [6 empty] | 2,400.1 - 3,000

## TM (hidden)
Sheet number | Sheet name | Input | English text | Welsh text | English text 2 | Welsh text 2 | English text 3 | Welsh text 3
0 | all | Link 1 | Instructions | Cyfarwyddiadau
0 | all | Link 2 | Start | Dechrau |  |  |  | Blaenau Gwent | Blaenau Gwent, Monmouthshire, Newport, Powys, Torfaen
0 | all | Link 3 | Stage 1 | Cam 1 |  |  |  | Monmouthshire
0 | all | Link 4 | Stage 2 | Cam 2 |  |  |  | Newport | Blaenau Gwent, Monmouthshire, Newport, Powys, Torfaen
0 | all | Link 5 | Stage 3 | Cam 3 |  |  |  | Powys
0 | all | Link 6 | Stage 3S | Cam 3S
0 | all | Link 7 | Stage 4 | Cam 4 |  |  |  | Torfaen
0 | all | Link 8 | Descriptions | Disgrifiadau
|  | Title | Nutrient Budget Calculator for Special Areas of Conservation (SACs) in Wales | Cyfrifiannell Cyllideb Maetholion ar gyfer Ardaloedd Cadwraeth Arbennig (ACA) yng Nghymru
|  | Text 1 | This calculator was created by Ricardo Energy and Environment and Arup for Welsh Government. | Crëwyd y gyfrifiannell hon gan Ricardo Energy and Environment ac Arup ar gyfer Llywodraeth Cymru.
|  |  | This is the English version of the calculator. This calculator is also available in Welsh/Cymraeg. | Dyma fersiwn Saesneg y gyfrifiannell. Mae'r gyfrifiannell hon hefyd ar gael yn Saesneg/English.
|  |  | This calculator contains 6 worksheets with 11 tables in total. | Mae'r gyfrifiannell hon yn cynnwys 6 taflen waith gyda chyfanswm o 11 tabl.
|  |  | This is the instructions cover sheet. It tells you how to use the calculator and gives an overview of each worksheet. | Dyma ddalen glawr y cyfarwyddiadau. Mae'n dweud wrthych sut i ddefnyddio'r gyfrifiannell ac yn rhoi trosolwg o bob taflen waith.
|  |  | You can move between worksheets using the tabs at the bottom of the page. | Gallwch symud rhwng taflenni gwaith gan ddefnyddio'r tabiau ar waelod y dudalen.
|  |  | If you use screen reading software, you can use 'Ctrl' + 'Page Down' keys to move between the tabs. | Os ydych yn defnyddio meddalwedd darllen sgrin, gallwch ddefnyddio bysellau 'Ctrl' + 'Page Down' i symud rhwng y tabiau.
|  |  | If you use a keyboard only, to open any link in this cover sheet first select the cell with the link and then press the 'Shift' + 'F10' keys or the 'Fn' + the 'Menu' keys, then press the letter 'O' twice to highlight 'Open Hyperlink' and press 'Enter'. | Os ydych yn defnyddio bysellfwrdd yn unig, i agor unrhyw ddolen ar y ddalen glawr hon yn gyntaf dewiswch y gell gyda'r ddolen ac yna pwyswch y bysellau 'Shift' + 'F10' neu'r bysellau 'Fn' + 'Dewislen', yna gwasgwch y llythyren 'O' ddwywaith i amlygu 'Open Hyperlink' a gwasgwch 'Enter'.
|  |  | If you use a keyboard only, access dropdown lists by clicking the dropdown arrow or pressing the 'Alt' + 'Down' keys when the cell is selected. | Os ydych chi'n defnyddio bysellfwrdd yn unig, cyrchwch restrau cwympo trwy glicio ar y saeth cwymplen neu wasgu'r bysellau 'Alt' + 'Down' pan fydd y gell yn cael ei dewis.
|  |  | Table of Contents | Tabl Cynnwys
|  |  | Topic of each worksheet | Testun pob taflen waith
|  |  | Stage 1: additional nutrient loading from wastewater | Cam 1: llwytho maetholion ychwanegol o ddŵr gwastraff
|  |  | Stage 2: nutrient loading from pre-existing landcovers | Cam 2: llwytho maetholion o orchudd tir sy'n bodoli eisoes
|  |  | Stage 3: nutrient loading from new landcovers | Cam 3: llwytho maetholion o orchudd tir newydd
|  |  | Stage 3S: nutrient load removed through sustainable urban drainage systems (SuDS) | Cam 3S: llwyth maethol yn cael ei dynnu drwy systemau draenio trefol cynaliadwy (SuDS)
|  |  | Stage 3S: nutrient load removed through SuDS | Cam 3S: llwyth maethol yn cael ei dynnu drwy SDCau
|  |  | Stage 4: final nutrient budget calculation | Cam 4: cyfrifiad terfynol y gyllideb faetholion
|  |  | General information about the calculator | Gwybodaeth gyffredinol am y gyfrifiannell
|  |  | This calculator helps you calculate a nutrient budget for a new development within one of the nine Special Areas of Conservation (SACs) within Wales. | Mae'r cyfrifiannell hwn yn eich helpu i gyfrifo cyllideb faetholion ar gyfer datblygiad newydd o fewn un o'r naw Ardal Cadwraeth Arbennig (ACA) yng Nghymru.
|  |  | The development categories include: residential; commercial; tourism; leisure and public service infrastructure. The planning permission use classes have been categorised into each development category. These can be found in the guidance that accompanies this calculator. | Mae'r categorïau datblygu yn cynnwys: preswyl; masnachol; twristiaeth; seilwaith hamdden a gwasanaethau cyhoeddus. Mae'r dosbarthiadau defnydd caniatâd cynllunio wedi'u categoreiddio i bob categori datblygu. Mae'r rhain i'w gweld yn y canllawiau sy'n cyd-fynd â'r gyfrifiannell hon.
|  |  | The nutrient budget for a site is calculated in 4 key stages with an additional optional stage in which information about the SuDS features on the site can be entered. Each stage is implemented in worksheets 2 to 6 of this calculator. | Mae'r gyllideb faetholion ar gyfer safle yn cael ei chyfrifo mewn 4 cyfnod allweddol gyda cham dewisol ychwanegol lle gellir mewnbynnu gwybodaeth am nodweddion SDCau ar y safle. Gweithredir pob cam yn nhaflenni gwaith 2 i 6 y gyfrifiannell hon.
|  |  | The instructions for completing each stage of the nutrient budget methodology are shown in cell A2 of each worksheet. Additional instructions may also be in cell A3. | Dangosir y cyfarwyddiadau ar gyfer cwblhau pob cam o'r fethodoleg cyllideb faetholion yng nghell A2 pob taflen waith. Gall cyfarwyddiadau ychwanegol fod yng nghell A3 hefyd.
|  |  | Each worksheet is connected through a set of formulas which calculate the final nutrient budget. The formulas use a set of lookup tables to find relevant values to determine the nutrient loading at each stage. | Mae pob taflen waith wedi'i chysylltu trwy set o fformiwlâu sy'n cyfrifo'r gyllideb faetholion derfynol. Mae'r fformiwlâu yn defnyddio set o dablau chwilio i ddod o hyd i werthoedd perthnasol i bennu'r llwyth maetholion ym mhob cam.
|  |  | Before a nutrient budget can be completed using the methodology, certain site-specific details for the development site need to be determined and entered into Stage 1, Stage 2, Stage 3, and Stage 3S (if applicable). | Cyn y gellir cwblhau cyllideb faetholion gan ddefnyddio’r fethodoleg, mae angen pennu manylion safle-benodol penodol ar gyfer y safle datblygu a’u cynnwys yng Ngham 1, Cam 2, Cam 3, a Cham 3S (os yw’n berthnasol).
|  |  | The total phosphorus (TP) budget and total nitrogen (TN) generated is calculated automatically once all required inputs have been entered into Stage 1, Stage 2, Stage 3, and Stage 3S (if applicable). The calculation involves adding the values from Stage 1 and the result of Stage 3 subtract Stage 3S (if applicable), and then subtracting the values from the Stage 2. A 20% precautionary buffer is then added to the result. This calculation is completed automatically in the Stage 4 worksheet. This equation can be summarised as: (Stage 1 - Stage 2 + (Stage 3 - Stage 3S)) * 1.2 = Stage 4 | Mae cyfanswm y gyllideb ffosfforws (TP) a chyfanswm y nitrogen (TN) a gynhyrchir yn cael eu cyfrifo'n awtomatig unwaith y bydd yr holl fewnbynnau gofynnol wedi'u cynnwys yng Ngham 1, Cam 2, Cam 3, a Cham 3S (os yw'n berthnasol). Mae'r cyfrifiad yn cynnwys adio'r gwerthoedd o Gam 1 a chanlyniad Cam 3 tynnu Cam 3S (os yw'n berthnasol), ac yna tynnu'r gwerthoedd o Gam 2. Yna mae byffer rhagofalus o 20% yn cael ei ychwanegu at y canlyniad. Cwblheir y cyfrifiad hwn yn awtomatig yn nhaflen waith Cam 4. Gellir crynhoi'r hafaliad hwn fel: (Cam 1 - Cam 2 + (Cam 3 - Cam 3S)) * 1.2 = Cam 4
|  |  | The pre-populated values in this calculator have been identified through extensive research and modelling. The values are based on the best available evidence and are suitably precautionary to account for any uncertainty. This nutrient budget calculator can be used as supporting evidence for a Habitat Regulations Assessment (HRA). Specifically, this calculator can be used within an appropriate assessment to assess the likely significant effects of a proposal on the integrity of the site and its conservation objectives. It is highly unadvisable to edit the values in this tool without a sufficient evidence base to justify any changes. | Mae'r gwerthoedd a ragboblogwyd yn y gyfrifiannell hon wedi'u nodi trwy waith ymchwil a modelu helaeth. Mae'r gwerthoedd yn seiliedig ar y dystiolaeth orau sydd ar gael ac maent yn ddigon rhagofalus i roi cyfrif am unrhyw ansicrwydd. Gellir defnyddio'r gyfrifiannell cyllideb faetholion hon fel tystiolaeth ategol ar gyfer Asesiad Rheoliadau Cynefinoedd (HRA). Yn benodol, gellir defnyddio'r gyfrifiannell hon o fewn asesiad priodol i asesu effeithiau sylweddol tebygol cynnig ar gyfanrwydd y safle a'i amcanion cadwraeth. Mae'n annoeth iawn golygu'r gwerthoedd yn yr offeryn hwn heb sylfaen dystiolaeth ddigonol i gyfiawnhau unrhyw newidiadau.
|  |  | When using this tool, it is recommended that you save a new copy of this workbook for each nutrient budget calculation, in order to retain a default blank copy. It may also be useful to open two calculators with one showing the instructions and one showing the calculator. | Wrth ddefnyddio'r offeryn hwn, argymhellir eich bod yn cadw copi newydd o'r llyfr gwaith hwn ar gyfer pob cyfrifiad cyllideb faetholion, er mwyn cadw copi gwag rhagosodedig. Gall fod yn ddefnyddiol hefyd agor dwy gyfrifiannell gydag un yn dangos y cyfarwyddiadau ac un yn dangos y gyfrifiannell.
|  |  | Notes on Stage 1: additional nutrient loading from wastewater | Nodiadau ar Gam 1: llwytho maetholion ychwanegol o ddŵr gwastraff
|  |  | The Stage 1 Worksheet contains 2 tables that are used to calculate the nutrient load associated with the additional wastewater generated as a result of the development. | Mae Taflen Waith Cam 1 hon yn cynnwys 2 dabl a ddefnyddir i gyfrifo’r llwyth maetholion sy’n gysylltiedig â’r dŵr gwastraff ychwanegol a gynhyrchir o ganlyniad i’r datblygiad.
|  |  | The first table under the heading 'Wastewater load input data' requires you to enter key information about the development and the water infrastructure. This table contains a mix of user inputs and values that are calculated automatically depending on the user inputs. | Mae'r tabl cyntaf o dan y pennawd 'Data mewnbwn llwyth dŵr gwastraff' yn gofyn i chi roi gwybodaeth allweddol am y datblygiad a'r seilwaith dŵr. Mae'r tabl hwn yn cynnwys cymysgedd o fewnbynnau defnyddwyr a gwerthoedd sy'n cael eu cyfrifo'n awtomatig yn dibynnu ar fewnbynnau'r defnyddiwr.
|  |  | The first table contains a postcode search function that allows you to find the appropriate LPA and the rainfall for the site if a valid postcode is entered that is within the SAC catchment. Entering the postcode for the site, or the nearest postcode, will generate site specific information. This automatically generated information can be used instead of manually entering the relevant data. However it is your responsibility to confirm this information is correct. | Mae’r tabl cyntaf yn cynnwys swyddogaeth chwilio cod post sy’n eich galluogi i ddod o hyd i’r LPA priodol a’r glawiad ar gyfer y safle os caiff cod post dilys ei nodi sydd o fewn dalgylch yr ACA. Bydd nodi cod post y safle, neu'r cod post agosaf, yn cynhyrchu gwybodaeth benodol i'r safle. Gellir defnyddio'r wybodaeth hon a gynhyrchir yn awtomatig yn lle mewnbynnu'r data perthnasol â llaw. Fodd bynnag, eich cyfrifoldeb chi yw cadarnhau bod y wybodaeth hon yn gywir.
|  |  | The amount of wastewater generated needs to be calculated using the following: - the SAC relevant to the development - project type (residential, commercial, tourism, public service infrastructure or leisure) - number of additional dwellings/units being created - the local planning authority (LPA) - an average occupancy rate (if applicable) - number of people/customers/employees per unit - a per capita water usage figure per person/customer/employee - the number of customers/users & employees (if applicable) - the percentage of customers/users & employees from outside the catchment (if applicable) - the water usage per customer/user (if applicable) | Mae angen cyfrifo faint o ddŵr gwastraff a gynhyrchir gan ddefnyddio'r canlynol: - yr ACA sy'n berthnasol i'r datblygiad - math o brosiect (preswyl, masnachol, twristiaeth, seilwaith gwasanaethau cyhoeddus neu hamdden) - nifer yr anheddau/unedau ychwanegol sy'n cael eu creu - yr awdurdod cynllunio lleol (ACLl) - cyfradd defnydd gyfartalog (os yw'n berthnasol) - nifer y bobl/cwsmeriaid/gweithwyr fesul uned - ffigur defnydd dŵr y pen fesul person/cwsmer/gweithiwr - nifer y cwsmeriaid/defnyddwyr a gweithwyr (os yn berthnasol) - canran y cwsmeriaid/defnyddwyr a gweithwyr o'r tu allan i'r dalgylch (os yw'n berthnasol) - y defnydd o ddŵr fesul cwsmer/defnyddiwr (os yw'n berthnasol)
|  |  | You must select the Special Area of Conservation (SAC) for the calculator to function correctly. | Rhaid i chi ddewis yr Ardal Cadwraeth Arbennig (ACA) er mwyn i'r gyfrifiannell weithio'n gywir.
|  |  | You must select the project type because it determines which inputs are required to calculate the amount of wastewater generated. The project types are representative of the planning permission uses classes. The appropriate project type for each planning permission use class can be found in the guidance that accompanies this calculator. | Rhaid i chi ddewis y math o brosiect oherwydd ei fod yn pennu pa fewnbynnau sydd eu hangen i gyfrifo faint o ddŵr gwastraff a gynhyrchir. Mae'r mathau o brosiectau yn gynrychioliadol o ddosbarthiadau defnydd caniatâd cynllunio. Mae’r math priodol o brosiect ar gyfer pob dosbarth defnydd caniatâd cynllunio i’w weld yn y canllawiau sy’n cyd-fynd â’r gyfrifiannell hon.
|  |  | The average occupancy rate for residential developments is dependent on the postcode entered or the LPA selected. The default water usage values is preset in the worksheet. The default setting for the average occupancy rate is preset in the worksheet and automatically generated dependant on the LPA. You can change this value if there is sufficient evidence that the development will be different to the national average. The per capita water usage is also present in the worksheet, this value should remain unchanged unless other efficiency measures are used. The number of new developments is not preset and must be a whole number. | Mae'r gyfradd ddeiliadaeth gyfartalog ar gyfer datblygiadau preswyl yn dibynnu ar y cod post a gofnodwyd neu'r ACLl a ddewiswyd. Mae'r gwerthoedd defnydd dŵr rhagosodedig wedi'u rhagosod yn y daflen waith. Mae'r gosodiad rhagosodedig ar gyfer y gyfradd ddeiliadaeth gyfartalog wedi'i ragosod yn y daflen waith ac yn cael ei gynhyrchu'n awtomatig yn dibynnu ar yr LPA. Gallwch newid y gwerth hwn os oes digon o dystiolaeth y bydd y datblygiad yn wahanol i'r cyfartaledd cenedlaethol. Mae'r defnydd dŵr y pen hefyd yn bresennol yn y daflen waith, ni ddylai'r gwerth hwn newid oni bai bod mesurau effeithlonrwydd eraill yn cael eu defnyddio. Nid yw nifer y datblygiadau newydd yn rhagosodedig a rhaid iddo fod yn rhif cyfan.
|  |  | You must select the wastewater treatment works (WwTW) that will receive the wastewater from the development. If you are unsure which WwTW will receive the wastewater, please obtain this information from Dwr Cymru/Welsh Water in order to complete this calculator. If connecting to a sewerage network is unfeasible and a septic tank or package treatment plant is being used, please select the appropriate option. | Rhaid i chi ddewis y gwaith trin dŵr gwastraff (GTDG) a fydd yn derbyn y dŵr gwastraff o'r datblygiad. Os nad ydych yn siŵr pa GTDG fydd yn derbyn y dŵr gwastraff, gofynnwch am y wybodaeth hon gan Dŵr Cymru/Welsh Water er mwyn cwblhau’r gyfrifiannell hon. Os yw cysylltu â rhwydwaith carthffosiaeth yn anymarferol a bod tanc septig neu offer trin pecyn yn cael ei ddefnyddio, dewiswch yr opsiwn priodol.
|  |  | The WwTW are correct at the time of publication but may be subject to change in the future. If required, these values will be updated at a later date accordingly. | Roedd y GTDG yn gywir ar adeg cyhoeddi ond efallai y byddant yn newid yn y dyfodol. Os bydd angen, caiff y gwerthoedd hyn eu diweddaru yn ddiweddarach yn unol â hynny.
|  |  | If you are using a septic tank or package treatment plant and the total nitrogen (TN) or total phosphorus (TP) final effluent concentrations are specified by the manufacturer, select 'Septic Tank user defined' or 'Package Treatment Plant user defined' and enter the manufacturer specified value in the cell where prompted (in mg/l). | Os ydych chi'n defnyddio tanc septig neu offer trin pecyn a bod y gwneuthurwr yn pennu cyfanswm crynodiadau elifiant terfynol cyfanswm nitrogen (TN) neu gyfanswm ffosfforws (TP), dewiswch 'Defnyddiwr Tanc Septig wedi'i ddiffinio' neu 'Defnyddiwr Offer Trin Pecyn wedi'i ddiffinio' a nodwch nododd y gwneuthurwr werth penodol yn y gell lle cafodd ei annog (mewn mg/l).
|  |  | The second table under the heading 'Final calculation of nutrient load from wastewater' contains the calculation of the nutrient load from additional wastewater generated by the development. | Mae'r ail dabl o dan y pennawd 'Cyfrifiad terfynol o lwyth maetholion o ddŵr gwastraff' yn cynnwys cyfrifiad y llwyth maetholion o ddŵr gwastraff ychwanegol a gynhyrchir gan y datblygiad.
|  |  | Notes on Stage 2: nutrient loading from pre-existing landcovers | Nodiadau ar Gam 2: llwytho maetholion o orchudd tir a oedd yn bodoli eisoes
|  |  | The Stage 2 Worksheet contains 2 tables that are used for calculating the annual nutrient load from existing (pre-development) landcovers within the redline boundary of the development. | Mae Taflen Waith cam 2 hon yn cynnwys 2 dabl a ddefnyddir ar gyfer cyfrifo'r llwyth maetholion blynyddol o orchudd tir presennol (cyn datblygu) o fewn ffin goch y datblygiad.
|  |  | The first table under the heading 'Physical characteristics' requires user inputs. You must select the predominant soil drainage present within the redline boundary of the site. The rainfall value will be automatically generated if the user has entered a valid postcode in 'Stage 1'. You must select whether the rainfall value is correct. If the rainfall value is not correct, or if a valid postcode has not been entered, you must select the rainfall value from the dropdown list. The sources of the soil drainage type and the rainfall can be found in the table under the heading 'Sources of information required for Stage 2' that follows this text. | Mae'r tabl cyntaf o dan y pennawd 'Nodweddion corfforol' yn gofyn am fewnbynnau defnyddwyr. Rhaid i chi ddewis y prif ddraeniad pridd sy'n bresennol o fewn ffin goch y safle. Bydd y gwerth glawiad yn cael ei gynhyrchu'n awtomatig os yw'r defnyddiwr wedi nodi cod post dilys yng Ngham 1. Rhaid i chi ddewis a yw'r gwerth glawiad yn gywir. Os nad yw'r gwerth glawiad yn gywir, neu os nad yw cod post dilys wedi'i nodi, rhaid i chi ddewis y gwerth glawiad o'r gwymplen. Mae ffynonellau’r math o ddraeniad pridd a’r glawiad i’w gweld yn y tabl o dan y pennawd ‘Ffynonellau gwybodaeth sydd eu hangen ar gyfer Cam 2’ sy’n dilyn y testun hwn.
|  |  | The second table under the heading 'Pre-existing landcovers' requires user inputs. You must select the most appropriate landcovers from a dropdown list of 18 landcover types to represent the landcover present on the site before the development. You must also enter the area of each landcover in hectares. The dropdown list contains 10 agricultural landcover types and 8 non-agricultural landcover types to represent the landcovers present on the site before development. The descriptions of each landcover type can be found in the guidance that accompanies this calculator. You must determine which landcover types are present within the redline boundary of the development before completing this tool. If there is a landcover within the development area that is not in the dropdown list please select the most similar landcover type. | Mae'r ail dabl o dan y pennawd 'Gorchuddion tir sy'n bodoli eisoes' yn gofyn am fewnbynnau defnyddwyr. Rhaid i chi ddewis y gorchudd tir mwyaf priodol o restr gwympo o 18 math o orchudd tir i gynrychioli'r gorchudd tir sy'n bresennol ar y safle cyn y datblygiad. Rhaid i chi hefyd nodi arwynebedd pob gorchudd tir mewn hectarau. Mae'r gwymplen yn cynnwys 10 math o orchudd tir amaethyddol ac 8 math o orchudd tir an-amaethyddol i gynrychioli'r gorchudd tir a oedd yn bresennol ar y safle cyn datblygu. Mae disgrifiadau o bob math o orchudd tir i'w gweld yn y canllawiau sy'n cyd-fynd â'r gyfrifiannell hon. Rhaid i chi benderfynu pa fathau o orchudd tir sy'n bresennol o fewn ffin llinell goch y datblygiad cyn cwblhau'r offeryn hwn. Os oes gorchudd tir o fewn yr ardal ddatblygu nad yw yn y gwymplen dewiswch y math gorchudd tir tebycaf.
|  |  | Sources of information required for Stage 2 | Ffynonellau gwybodaeth sydd eu hangen ar gyfer Cam 2
|  |  | Description of information | Disgrifiad o'r wybodaeth
|  |  | Soil drainage: The drainage associated with the predominant soil type within the development site can be found using the Soilscapes Map. | Draeniad pridd: Gellir dod o hyd i'r draeniad sy'n gysylltiedig â'r prif fath o bridd o fewn y safle datblygu trwy ddefnyddio'r Map Priddweddau.
|  |  | Rainfall: The annual average rainfall that the development will receive can be found using the National River Flow Archive. You must first select any flow gauging station. You must navigate to the 'Catchment info' tab and select the spatial data type to view as 'Rainfall'. You can scroll around this map to find your development. Clicking the link will take the user to the 'Usk at Chainbridge' station. | Glawiad: Gellir dod o hyd i’r glawiad cyfartalog blynyddol y bydd y datblygiad yn ei dderbyn gan ddefnyddio’r Archif Genedlaethol Llif Afonydd. Yn gyntaf rhaid i chi ddewis unrhyw orsaf medryddu llif. Rhaid i chi lywio i'r tab 'Gwybodaeth Dalgylch' a dewis y math o ddata gofodol i'w weld fel 'Glawiad'. Gallwch sgrolio o amgylch y map hwn i ddod o hyd i'ch datblygiad. Bydd clicio ar y ddolen yn mynd â'r defnyddiwr i orsaf 'Usk at Chainbridge'.
|  |  | Notes on Stage 3: nutrient loading from new landcovers | Nodiadau ar Gam 3: llwytho maetholion o orchudd tir newydd
|  |  | The Stage 3 Worksheet contains one table which is used to calculate the annual nutrient load from new (post-development) landcovers within the redline boundary of the development. The type(s) and area(s) of landcover present on the new development is required to generate nutrient loads associated with the current landcovers on the site. | Mae Taflen Waith Cam 3 hon yn cynnwys un tabl a ddefnyddir i gyfrifo’r llwyth maetholion blynyddol o orchudd tir newydd (ar ôl datblygu) o fewn ffin llinell goch y datblygiad. Mae angen y math(au) a'r ardal(oedd) o orchudd tir sy'n bresennol ar y datblygiad newydd i gynhyrchu llwythi maethol sy'n gysylltiedig â'r gorchudd tir presennol ar y safle.
|  |  | The second table under the heading 'New landcovers' requires user inputs. You must select the most appropriate landcovers from a dropdown list of 18 landcover types to represent the landcover present on the site following the development. You must also enter the area of each landcover in hectares. The dropdown list contains 10 agricultural landcover types and 8 non-agricultural landcover types to represent the landcovers present on the site before development. The descriptions of each landcover type can be found in the guidance that accompanies this calculator. You must determine which landcover types are present within the redline boundary of the development before completing this tool. If there is a landcover within the development area that is not in the dropdown list please select the most similar landcover type. | Mae'r ail dabl o dan y pennawd 'Gorchuddion tir newydd' yn gofyn am fewnbynnau defnyddwyr. Rhaid i chi ddewis y gorchudd tir mwyaf priodol o restr gwympo o 18 math o orchudd tir i gynrychioli'r gorchudd tir sy'n bresennol ar y safle yn dilyn y datblygiad. Rhaid i chi hefyd nodi arwynebedd pob gorchudd tir mewn hectarau. Mae'r gwymplen yn cynnwys 10 math o orchudd tir amaethyddol ac 8 math o orchudd tir an-amaethyddol i gynrychioli'r gorchudd tir a oedd yn bresennol ar y safle cyn datblygu. Mae disgrifiadau o bob math o orchudd tir i'w gweld yn y canllawiau sy'n cyd-fynd â'r gyfrifiannell hon. Rhaid i chi benderfynu pa fathau o orchudd tir sy'n bresennol o fewn ffin llinell goch y datblygiad cyn cwblhau'r offeryn hwn. Os oes gorchudd tir o fewn yr ardal ddatblygu nad yw yn y gwymplen dewiswch y math gorchudd tir tebycaf.
|  |  | Notes on Stage 3S: nutrient load removed through SuDS | Nodiadau ar Gam 3S: llwyth maethol yn cael ei dynnu drwy SuDS
|  |  | The Stage 3S Worksheet contains one table in which you can enter key information about the use of SuDS to treat the runoff from the site and reduce the nutrient loading from new landcovers. | Mae Taflen Waith Cam 3S hon yn cynnwys un tabl lle gallwch fewnbynnu gwybodaeth allweddol am y defnydd o SuDS i drin y dŵr ffo o’r safle a lleihau’r llwyth maetholion o orchudd tir newydd.
|  |  | In this section the user will need to enter information about the SuDS features used to calculate the amount of nutrients removed through SuDS treatment of surface runoff. This section must only be completed if SuDS are compliant with the national standards and are being implemented under the requirement of the Flood and Water Management Act 2010 (Schedule 3). Any SuDS that are being implemented in addition to the site plans for the purposes of mitigation must not be considered in the nutrient budget calculation for the site. In this instance, it is instead recommended that a second calculation is populated - the People over Wind judgment means that it is no longer possible to apply mitigation measures at the screening stage. | Yn yr adran hon bydd angen i’r defnyddiwr fewnbynnu gwybodaeth am y nodweddion SuDS a ddefnyddir i gyfrifo faint o faetholion sy’n cael eu tynnu drwy driniaeth SuDS o ddŵr ffo arwyneb. Rhaid llenwi’r adran hon dim ond os yw SDCau yn cydymffurfio â’r safonau cenedlaethol ac yn cael eu gweithredu o dan ofyniad Deddf Rheoli Llifogydd a Dŵr 2010 (Atodlen 3). Ni ddylai unrhyw SDCau sy'n cael eu gweithredu yn ychwanegol at y cynlluniau safle at ddibenion lliniaru gael eu hystyried wrth gyfrifo cyllideb faetholion y safle. Yn yr achos hwn, argymhellir yn lle hynny y dylid llenwi ail gyfrifiad - mae dyfarniad People over Wind yn golygu nad yw bellach yn bosibl defnyddio mesurau lliniaru yn y cam sgrinio.
|  |  | The landcovers and areas present on the new site will be automatically populated from Stage 3. | Bydd y gorchuddion tir a’r ardaloedd sy’n bresennol ar y safle newydd yn cael eu poblogi’n awtomatig o Gam 3.
|  |  | You will need to: - enter the catchment area that drains to the SuDS as a proportion of the new landcovers - choose the SuDS features used - enter the nutrient removal rates as a percentage | Bydd angen i chi: - fynd i mewn i'r dalgylch sy'n draenio i'r SDCau fel cyfran o'r gorchudd tir newydd - dewis y nodweddion SDC a ddefnyddir - nodi'r cyfraddau tynnu maetholion fel canran
|  |  | It is recommended that the surface area of the SuDS features are included within the area of the landcover that they drain. If required, you can split the landcover up in Stage 3 to demonstrate multiple drainage configurations. You can select a SuDS feature from a list of 23 options. If a SuDS management train that comprises multiple SuDS features is being implemented you should select the appropriate option from the start of the list. Otherwise, you should select the individual SuDS feature being used. If the appropriate SuDS feature cannot be found in the list, select the most relevant alternative. The nutrient removal rates should be entered as a whole number percentage between 0-100. You must be able to provide evidence for the removal rates you have entered. This is likely to require the submission of a drainage assessment and a detailed design of the SuDS features. | Argymhellir bod arwynebedd y nodweddion SuDS yn cael ei gynnwys o fewn ardal y gorchudd tir y maent yn ei ddraenio. Os oes angen, gallwch rannu'r gorchudd tir yng Ngham 3 i ddangos ffurfweddiadau draenio lluosog. Gallwch ddewis nodwedd SDCau o restr o 23 opsiwn. Os yw trên rheoli SDCau sy'n cynnwys nifer o nodweddion SuDS yn cael ei weithredu, dylech ddewis yr opsiwn priodol o ddechrau'r rhestr. Fel arall, dylech ddewis y nodwedd SDCau unigol a ddefnyddir. Os na ellir dod o hyd i'r nodwedd SDCau briodol yn y rhestr, dewiswch y dewis arall mwyaf perthnasol. Dylid nodi'r cyfraddau tynnu maetholion fel canran rhif cyfan rhwng 0-100. Mae'n rhaid i chi allu darparu tystiolaeth ar gyfer y cyfraddau dileu rydych wedi'u nodi. Mae hyn yn debygol o olygu bod angen cyflwyno asesiad draenio a dyluniad manwl o nodweddion SDCau.
|  |  | The amount of nutrients removed through SuDS is automatically calculated using the landcovers and associated loads from Stage 3, the drainage area, and the nutrient removal rates. The total load removed through SuDS is incorporated into the final nutrient budget calculation. Selecting the type of SuDS feature used is to ensure that the nutrient budget calculator matches the SuDS design detailed in the planning application. | Mae faint o faetholion sy'n cael eu tynnu drwy SuDS yn cael ei gyfrifo'n awtomatig gan ddefnyddio'r gorchudd tir a'r llwythi cysylltiedig o Gam 3, yr ardal ddraenio, a'r cyfraddau tynnu maetholion. Mae cyfanswm y llwyth sy'n cael ei dynnu drwy SDCau wedi'i ymgorffori yng nghyfrifiad terfynol y gyllideb faetholion. Mae dewis y math o nodwedd SDCau a ddefnyddir er mwyn sicrhau bod y gyfrifiannell cyllideb faetholion yn cyd-fynd â’r cynllun SDCau a nodir yn y cais cynllunio.
|  |  | Further information on SuDS can be found in the table under the heading 'Sources of information on SuDS and how to design them for nutrient removal' that follows this text. | Ceir rhagor o wybodaeth am SDCau yn y tabl o dan y pennawd 'Ffynonellau gwybodaeth am SDCau a sut i'w dylunio ar gyfer tynnu maetholion' sy'n dilyn y testun hwn.
|  |  | Sources of information on SuDS and how to design them for nutrient removal | Ffynonellau gwybodaeth am SDCau a sut i'w dylunio i gael gwared ar faetholion
|  |  | Description of information | Disgrifiad o'r wybodaeth
|  |  | National standards for sustainable drainage systems (SuDS) can be found here: | Mae safonau cenedlaethol ar gyfer systemau draenio cynaliadwy (SDCau) i’w gweld yma:
|  |  | Ciria's Using SuDS to reduce nitrogen in surface water runoff (C815) can be found here: | Mae Ciria's yn Defnyddio SDCau i leihau nitrogen mewn dŵr ffo wyneb (C815) i'w weld yma:
|  |  | Ciria's Using SuDS to reduce phosphorus in surface water runoff (C808F) can be found here: | Mae Ciria's yn Defnyddio SDCau i leihau ffosfforws mewn dŵr ffo wyneb (C808F) i'w weld yma:
|  |  | Notes about the final annual nutrient budget | Nodiadau am y gyllideb faetholion flynyddol derfynol
|  |  | The Stage 4 Worksheet contains 2 tables which calculate the TP budget and the amount of TN generated. | Mae Taflen Waith Cam 4 hon yn cynnwys 2 dabl sy’n cyfrifo’r gyllideb TP a swm y TN a gynhyrchir.
|  |  | The final stage automatically calculates the final nutrient budget using the results from Stage 1 to Stage 3S using the following equation: (Stage 1 - Stage 2 + (Stage 3 - Stage 3S)) * 1.2 = Stage 4 | Mae'r cam olaf hwn yn cyfrifo'r gyllideb faetholion terfynol yn awtomatig gan ddefnyddio'r canlyniadau o Gam 1 i Gam 3S gan ddefnyddio'r hafaliad canlynol: (Cam 1 - Cam 2 + (Cam 3 - Cam 3S)) * 1.2 = Cam 4
|  |  | The first table under the heading 'Total phosphorus budget' calculates the amount of TP that you need to mitigate. | Mae'r tabl cyntaf o dan y pennawd 'Cyfanswm y gyllideb ffosfforws' yn cyfrifo faint o TP y mae angen i chi ei liniaru.
|  |  | The second table under the heading 'Total nitrogen generated' calculates the amount of TN generated. | Mae'r ail dabl o dan y pennawd 'Cyfanswm y nitrogen a gynhyrchir' yn cyfrifo faint o TN a gynhyrchir.
|  | Text 2 | This calculator contains 6 worksheets with 12 tables in total. | Welsh translation of This calculator contains 6 worksheets with 12 tables in total.
|  | Text 3 | This is the instructions cover sheet. It tells you how to use the calculator and gives an overview of each worksheet. | Welsh translation of This is the instructions cover sheet. It tells you how to use the calculator and gives an overview of each worksheet.
|  | Text 4 | You can move between worksheets using the tabs at the bottom of the page. | Welsh translation of You can move between worksheets using the tabs at the bottom of the page.
|  | Text 5 | If you use screen reading software, you can use 'Ctrl' + 'Page Down' keys to move between the tabs. | Welsh translation of If you use screen reading software, you can use 'Ctrl' + 'Page Down' keys to move between the tabs.
|  | Text 6 | If you use a keyboard only, to open any link in this form first select the cell with the link and then press the 'Shift' + 'F10' keys or the 'Fn' + the 'Menu' keys, then press the letter 'O' twice to highlight 'Open Hyperlink' and press 'Enter'. | Welsh translation of If you use a keyboard only, to open any link in this form first select the cell with the link and then press the 'Shift' + 'F10' keys or the 'Fn' + the 'Menu' keys, then press the letter 'O' twice to highlight 'Open Hyperlink' and press 'Enter'.
|  | Text 7 | If you use a keyboard only, access dropdown lists by clicking the dropdown arrow or pressing the 'Alt' + 'Down' keys when the cell is selected. | Welsh translation of If you use a keyboard only, access dropdown lists by clicking the dropdown arrow or pressing the 'Alt' + 'Down' keys when the cell is selected.
|  | Table 1 subtitle | Table of Contents | Welsh translation of Table of Contents
|  | N/A | Not applicable | Ddim yn berthnasol
| Stage 1 | A2 text | This sheet contains 2 tables. The tables are separated by a heading, which describes the following table. The first table labelled 'Wastewater load input data' requires user inputs. Cells A8, A9, A13, A17 to A20, A22 to A23 are automatically generated and will state 'Not applicable' unless the required user inputs have been entered. You will need to fill in cells B6, B7, B10 to B12 and B14 to B23, unless the description states 'Not applicable'. Cells B8, B9, B13 are automatically generated and will state 'Not applicable' unless the user inputs have been entered. If the user does not enter a postcode in cell B7, cells A9 and B9 will state 'Not applicable', however this data can be selected in Cell B6 in Stage 2. Cells B24 and B25 are automatically generated and will state '0.00' unless the user inputs have been entered. The second table labelled 'Final calculation of nutrient load from wastewater' does not require any user inputs. Cells B28 to B31 are automatically generated and will state '0.00' unless the user inputs have been entered in the second table labelled 'Wastewater load calculation table'. | Mae'r daflen hon yn cynnwys 2 dabl. Mae'r tablau wedi'u gwahanu gan bennawd, sy'n disgrifio'r tabl canlynol. Mae'r tabl cyntaf sydd â'r label 'Data mewnbwn llwyth dŵr gwastraff' yn gofyn am fewnbynnau defnyddwyr. Mae celloedd A8, A9, A13, A17 i A20, A22 i A23 yn cael eu cynhyrchu'n awtomatig a byddant yn nodi 'Amherthnasol' oni bai bod y mewnbynnau defnyddiwr gofynnol wedi'u nodi. Bydd angen i chi lenwi celloedd B6, B7, B10 i B12 a B14 i B23, oni bai bod y disgrifiad yn nodi 'Amherthnasol'. Mae celloedd B8, B9, B13 yn cael eu cynhyrchu'n awtomatig a byddant yn datgan 'Amherthnasol' oni bai bod mewnbynnau'r defnyddiwr wedi'u nodi. Os nad yw'r defnyddiwr yn rhoi cod post yng nghell B7, bydd celloedd A9 a B9 yn nodi 'Amherthnasol', fodd bynnag gellir dewis y data hwn yng Nghell B6 yng Ngham 2. Mae celloedd B24 a B25 yn cael eu cynhyrchu'n awtomatig a byddant yn nodi '0.00' oni bai mae'r mewnbynnau defnyddiwr wedi'u cofnodi. Nid oes angen unrhyw fewnbynnau defnyddiwr ar gyfer yr ail dabl sy'n dwyn y teitl 'Cyfrifiad terfynol o lwyth maetholion o ddŵr gwastraff'. Mae celloedd B28 i B31 yn cael eu cynhyrchu'n awtomatig a byddant yn datgan '0.00' oni bai bod y mewnbynnau defnyddiwr wedi'u nodi yn yr ail dabl â'r label 'Tabl cyfrifo llwyth dŵr gwastraff'.
| Stage 1 | A3 text | How to fill in the table 'Wastewater load calculation table': Cell B6: Select the Special Area of Conservation (SAC) from the dropdown list. Cell B7: Enter the postcode, or the nearest postcode, for the proposed development site. This input is optional. Cell B10: Select the project type or development type from the dropdown list. Cell B11: Enter the number of additional units being created. Cell B12: Enter the Local Planning Authority the development is within, if a valid postcode has not been entered into cell B7. Cell B14: Select 'Yes' if the default occupancy rate is being used for the development if the project type is residential from the dropdown list. Select 'No' if the default occupancy rate does not apply to the residential development. Cell B15: Enter the average occupancy rate of the development if the default occupancy rate is not automatically generated in cell B13. Cell B16: Enter the water usage per resident or customer/user in litres per person per day. This value should be kept at 120 for residents unless other efficiency measures are used. Cell B17: Enter the percentage of customers/users coming from outside the catchment if the project type is not residential. The default value is set to 100%. Cell B18: Enter the number of employees per unit if the project type is not residential. Cell B19: Enter the water usage per resident or customer/user in litres per person per day. The default value is 120. Cell B20: Enter the percentage of employees coming from outside the catchment if the project type is not residential. The default value is set to 100%. Cell B21: Select the connecting wastewater treatment works (WwTW) from the dropdown list. Cell B22: Enter the certified value of total phosphorus (TP) if you select 'Package Treatment Plant user defined' or 'Septic Tank user defined' in cell B21. Otherwise the default values for these sewarage systems will be used in the calculation of the nutrient load associated with wastewater. Cell B23: Enter the certified value of total nitrogen (TN) if you select 'Package Treatment Plant user defined' or 'Septic Tank user defined' in cell B21. Otherwise the default values for these sewerage systems will be used in the calculation of the nutrient load associated with wastewater. | Sut i lenwi’r tabl ‘Tabl cyfrifo llwyth dŵr gwastraff’: Cell B6: Dewiswch yr Ardal Cadwraeth Arbennig (ACA) o'r gwymplen. Cell B7: Nodwch y cod post, neu'r cod post agosaf, ar gyfer safle'r datblygiad arfaethedig. Mae'r mewnbwn hwn yn ddewisol. Cell B10: Dewiswch y math o brosiect neu'r math o ddatblygiad o'r gwymplen. Cell B11: Nodwch nifer yr unedau ychwanegol sy'n cael eu creu. Cell B12: Ewch i mewn i'r Awdurdod Cynllunio Lleol y mae'r datblygiad ynddo, os nad oes cod post dilys wedi'i roi yng nghell B7. Cell B14: Dewiswch 'Ie' os yw'r gyfradd daliadaeth ddiofyn yn cael ei defnyddio ar gyfer y datblygiad os yw'r math o brosiect yn un preswyl o'r gwymplen. Dewiswch 'Na' os nad yw'r gyfradd daliadaeth ddiofyn yn berthnasol i'r datblygiad preswyl. Cell B15: Nodwch gyfradd daliadaeth gyfartalog y datblygiad os na chynhyrchir y gyfradd daliadaeth ddiofyn yn awtomatig yng nghell B13. Cell B16: Rhowch y defnydd o ddŵr fesul preswylydd neu gwsmer/defnyddiwr mewn litrau fesul person y dydd. Dylid cadw'r gwerth hwn ar 120 i breswylwyr oni bai bod mesurau effeithlonrwydd eraill yn cael eu defnyddio. Cell B17: Nodwch ganran y cwsmeriaid/defnyddwyr sy'n dod o'r tu allan i'r dalgylch os nad yw'r math o brosiect yn un preswyl. Mae'r gwerth diofyn wedi'i osod i 100%. Cell B18: Nodwch nifer y gweithwyr fesul uned os nad yw'r math o brosiect yn un preswyl. Cell B19: Rhowch y defnydd o ddŵr fesul preswylydd neu gwsmer/defnyddiwr mewn litrau fesul person y dydd. Y gwerth rhagosodedig yw 120. Cell B20: Nodwch ganran y gweithwyr sy'n dod o'r tu allan i'r dalgylch os nad yw'r math o brosiect yn un preswyl. Mae'r gwerth diofyn wedi'i osod i 100%. Cell B21: Dewiswch y gweithfeydd trin dŵr gwastraff cysylltiol (WwTW) o'r gwymplen. Cell B22: Rhowch werth ardystiedig cyfanswm ffosfforws (TP) os dewiswch 'Pecyn Triniaeth Defnyddiwr wedi'i ddiffinio gan y Defnyddiwr' neu 'Defnyddiwr Tanc Septig wedi'i ddiffinio' yng nghell B21. Fel arall, bydd y gwerthoedd rhagosodedig ar gyfer y systemau carthffosiaeth hyn yn cael eu defnyddio wrth gyfrifo'r llwyth maetholion sy'n gysylltiedig â dŵr gwastraff. Cell B23: Rhowch werth ardystiedig cyfanswm nitrogen (TN) os dewiswch 'Pecyn Triniaeth Defnyddiwr wedi'i ddiffinio gan y Defnyddiwr' neu 'Defnyddiwr Tanc Septig wedi'i ddiffinio' yng nghell B21. Fel arall, bydd y gwerthoedd rhagosodedig ar gyfer y systemau carthffosiaeth hyn yn cael eu defnyddio wrth gyfrifo'r llwyth maetholion sy'n gysylltiedig â dŵr gwastraff.
| Stage 2 | A2 text | This sheet contains 2 tables. The tables are separated by a heading, which describes the following table. The first table labelled 'Physical characteristics' requires user inputs. You will need to fill in cells B5, B7 and B8 unless the description states 'Not applicable'. Cell B6 is automatically generated and will state 'Not applicable' unless a valid postcode has been entered into the previous worksheet. The second table labelled 'Pre-exisiting landcovers' requires user inputs. You will need to fill in cells A11 to B25. Cells B26 and C11 to D26 are automatically generated and will state '0.00' unless the required user inputs have been entered. Row 26 automatically calculates the 'Total' sum of cells B11 to B25 in cell B26, C11 to C25 in C26, and D11 to D25 in D26. How to fill in the table 'Physical characteristics': Cell B5: Select the appropriate soil drainage for the site from the dropdown list. Cell B7: Select 'Yes' if the automatically populated rainfall value is correct for the site if a valid postcode has been entered into the worksheet titled 'Stage 1'. Select 'No' if the automatically populated rainfall value is incorrect if a valid postcode has been entered into the worksheet titled 'Stage 1'. Cell B8: Select the annual average rainfall the development will receive from the dropdown list if a valid postcode has not been entered into the worksheet titled 'Stage 1'. How to fill in the table 'Pre-existing landcovers': Cells A11 to A25: Select the current (pre-development) land covers present within the redline boundary of the site. Cells B11 to B25: Enter the area in hectares of each land cover. | Mae'r daflen hon yn cynnwys 2 dabl. Mae'r tablau wedi'u gwahanu gan bennawd, sy'n disgrifio'r tabl canlynol. Mae'r tabl cyntaf sydd â'r label 'Nodweddion ffisegol' yn gofyn am fewnbynnau defnyddwyr. Bydd angen i chi lenwi celloedd B5, B7 a B8 oni bai bod y disgrifiad yn nodi 'Amherthnasol'. Mae Cell B6 yn cael ei chynhyrchu'n awtomatig a bydd yn nodi 'Amherthnasol' oni bai bod cod post dilys wedi'i roi yn y daflen waith flaenorol. Mae'r ail dabl sydd â'r label 'Gorchuddion tir sy'n bodoli eisoes' yn gofyn am fewnbynnau defnyddwyr. Bydd angen i chi lenwi celloedd A11 i B25. Mae celloedd B26 a C11 i D26 yn cael eu cynhyrchu'n awtomatig a byddant yn nodi '0.00' oni bai bod y mewnbynnau defnyddiwr gofynnol wedi'u nodi. Mae rhes 26 yn cyfrifo swm 'Cyfanswm' celloedd B11 i B25 yn awtomatig yng nghell B26, C11 i C25 yn C26, a D11 i D25 yn D26. Sut i lenwi’r tabl ‘Nodweddion ffisegol’: Cell B5: Dewiswch y draeniad pridd priodol ar gyfer y safle o'r gwymplen. Cell B7: Dewiswch 'Ie' os yw'r gwerth glawiad a boblogwyd yn awtomatig yn gywir ar gyfer y safle os yw cod post dilys wedi'i roi yn y daflen waith o'r enw 'Cam 1'. Dewiswch 'Na' os yw'r gwerth glawiad a boblogwyd yn awtomatig yn anghywir os yw cod post dilys wedi'i roi yn y daflen waith o'r enw 'Cam 1'. Cell B8: Dewiswch y glawiad cyfartalog blynyddol y bydd y datblygiad yn ei dderbyn o'r gwymplen os nad oes cod post dilys wedi'i roi yn y daflen waith o'r enw 'Cam 1'. Sut i lenwi'r tabl 'Gorchuddion tir sy'n bodoli eisoes': Celloedd A11 i A25: Dewiswch y gorchuddion tir presennol (cyn datblygu) sy'n bresennol o fewn ffin goch y safle. Celloedd B11 i B25: Rhowch yr arwynebedd mewn hecatrau o bob gorchudd tir.
| Stage 3 | A2 text | This sheet contains one table. A heading describes the table. The table is labelled 'New landcovers'. You will need to fill in cells A5 to B19. Cells B20, C5 to D19 are automatically generated and will state '0.00' unless the required user inputs have been entered. Cells E5 to E19 are automatically populated and will state 'Not applicable' unless the total area of the landcovers does not match the total area of the landcovers in the worksheet titled 'Stage 2'. Row 20 automatically calculates the 'Total' sum of cells B5 to B19 in cell B20, C5 to C19 in C20, and D5 to D19 in D20. How to fill in the table 'New landcovers': Cells A5 to A19: Choose the new (post-development) land covers present within the redline boundary of the site. Cells B5 to B19: Enter the area in hectares of each land cover. | Mae'r daflen hon yn cynnwys un tabl. Mae pennawd yn disgrifio'r tabl. Mae'r tabl wedi'i labelu fel 'Gorchuddion tir newydd'. Bydd angen i chi lenwi celloedd A5 i B19. Mae celloedd B20, C5 i D19 yn cael eu cynhyrchu'n awtomatig a byddant yn nodi '0.00' oni bai bod y mewnbynnau defnyddiwr gofynnol wedi'u nodi. Mae celloedd E5 i E19 yn cael eu poblogi'n awtomatig a byddant yn datgan 'Amherthnasol' oni bai nad yw cyfanswm arwynebedd y gorchudd tir yn cyfateb i gyfanswm arwynebedd y gorchuddion tir yn y daflen waith o'r enw 'Cam 2'. Mae rhes 20 yn cyfrifo swm 'Cyfanswm' celloedd B5 i B19 yn awtomatig yng nghell B20, C5 i C19 yn C20, a D5 i D19 yn D20. Sut i lenwi'r tabl 'Gorchuddion tir newydd': Celloedd A5 i A19: Dewiswch y gorchuddion tir newydd (ar ôl datblygu) sy'n bresennol o fewn ffin coch y safle. Celloedd B5 i B19: Nodwch yr arwynebedd mewn hectarau o bob gorchudd tir.
| Stage 3S | A2 text | This sheet contains one table. A heading describes the table. The table is labelled 'SuDS information'. SuDS stands for sustainable urban drainage systems. Cells A5 to A19 are automatically populated with landcovers entered into the worksheet titled 'Stage 3' and will state 'Not applicable' if landcovers have not been entered into the corresponding cells in the worksheet titled 'Stage 3'. Cells B5 to B20 are automatically populated with the area in hectares of the landcovers entered into the worksheet titled 'Stage 3' and will state '0.00' if areas have not been entered into the worksheet titled 'Stage 3'. You will need to fill in cells C5 to F19. Cells G5 to H20 are automatically calculated and will state '0.00' unless the required inputs have been entered. Row 20 automatically calculates the 'Total' sum of cells B5 to B19 in cell B20, the sum of cells G5 to G19 in cell G20 and the sum of cells H5 to H19 in cell H20. How to fill in the table 'SuDS information': Cells C5 to C19: Enter the size of the catchment area that drains to the SuDS feature as a proportion (%) of the landcover in the areas (in hectares). Cells D5 to D19: Select the SuDS feature that is being used to treat the run off from the dropdown list. Cells E5 to E19: Enter the phosphorus removal rate of the nutrient inputs as a percentage (%). Cells F5 to F19: Enter the nitrogen removal rate of the nutrient inputs as a percentage (%). | Mae'r daflen hon yn cynnwys un tabl. Mae pennawd yn disgrifio'r tabl. Mae'r tabl wedi'i labelu â 'Gwybodaeth SuDS'. Ystyr SuDS yw systemau draenio trefol cynaliadwy. Mae celloedd A5 i A19 yn cael eu llenwi'n awtomatig â gorchuddion tir sy'n cael eu rhoi yn y daflen waith o'r enw 'Cam 3' a bydd yn nodi 'Amherthnasol' os nad yw gorchuddion tir wedi'u rhoi yn y celloedd cyfatebol yn y daflen waith o'r enw 'Cam 3'. Mae celloedd B5 i B20 yn cael eu llenwi'n awtomatig gyda'r arwynebedd mewn hectarau o'r gorchuddion tir a nodir yn y daflen waith o'r enw 'Cam 3' a byddant yn nodi '0.00' os nad yw ardaloedd wedi'u cynnwys yn y daflen waith o'r enw 'Cam 3'. Bydd angen i chi lenwi celloedd C5 i F19. Mae celloedd G5 i H20 yn cael eu cyfrifo'n awtomatig a byddant yn datgan '0.00' oni bai bod y mewnbynnau gofynnol wedi'u nodi. Mae rhes 20 yn cyfrifo swm 'Cyfanswm' celloedd B5 i B19 yng nghell B20 yn awtomatig, cyfanswm celloedd G5 i G19 yng nghell G20 a swm celloedd H5 i H19 yng nghell H20. Sut i lenwi'r tabl 'Gwybodaeth SuDS': Celloedd C5 i C19: Nodwch faint y dalgylch sy'n draenio i'r nodwedd SDCau fel cyfran (%) o'r gorchudd tir yn yr ardaloedd (mewn hectarau). Celloedd D5 i D19: Dewiswch y nodwedd SDCau sy'n cael ei defnyddio i drin y dŵr ffo o'r gwymplen. Celloedd E5 i E19: Nodwch gyfradd tynnu ffosfforws y mewnbynnau maetholion fel canran (%). Celloedd F5 i F19: Nodwch gyfradd tynnu nitrogen y mewnbynnau maetholion fel canran (%).
| Stage 4 | A2 text | This sheet contains 2 tables. The tables are separated by a heading, which describes the following table. The tables are automatically calculated using the outputs from the previous stages. The first table labelled 'Total phosphorus budget' presents the calculations that underpin the final total phosphorus (TP) budget in cell B10. The second table labelled 'Total nitrogen generated' presents the calculations that underpin the final total nitrogen (TN) budget in cell B18. You do not need to fill in any cells in the tables. Cells B5 to B10 and B13 to B18 are automatically calculated. Cells B5 to B9 and cells B13 to B17 will state '0.00' unless user inputs have been entered to all of the required stages. Cell B10 will state 'No TP mitigation needed' if the phosphorus budget is less than 0.00 kilograms TP per year. Cell B18 will state 'No additional TN generated' if the nitrogen budget is less than 0.00 kilograms TN per year. | Mae'r daflen hon yn cynnwys 2 dabl. Mae'r tablau wedi'u gwahanu gan bennawd, sy'n disgrifio'r tabl canlynol. Mae'r tablau'n cael eu cyfrifo'n awtomatig gan ddefnyddio'r allbynnau o'r camau blaenorol. Mae’r tabl cyntaf sydd â’r label ‘Cyfanswm y gyllideb ffosfforws’ yn cyflwyno’r cyfrifiadau sy’n sail i’r gyllideb ffosfforws (TP) derfynol yng nghell B10. Mae'r ail dabl sy'n dwyn y teitl 'Cyfanswm y nitrogen a gynhyrchwyd' yn cyflwyno'r cyfrifiadau sy'n sail i gyfanswm cyllideb derfynol nitrogen (TN) yng nghell B18. Nid oes angen i chi lenwi unrhyw gelloedd yn y tablau. Mae celloedd B5 i B10 a B13 i B18 yn cael eu cyfrifo'n awtomatig. Bydd celloedd B5 i B9 a chelloedd B13 i B17 yn nodi '0.00' oni bai bod mewnbynnau defnyddwyr wedi'u nodi ym mhob un o'r camau gofynnol. Bydd Cell B10 yn nodi 'Dim angen lliniaru TP' os yw'r gyllideb ffosfforws yn llai na 0.00 cilogram TP y flwyddyn. Bydd Cell B18 yn nodi 'Dim TN ychwanegol wedi'i gynhyrchu' os yw'r gyllideb nitrogen yn llai na 0.00 cilogram TN y flwyddyn.
1 | Introduction (Rhagymadrodd) | Title | Nutrient Budget Calculator for Wales | Cyfrifiannell Cyllideb Maetholion Cymru
1 | Introduction (Rhagymadrodd) | Subtitle | A tool for assessing the phosphorus and nitrogen loading to Special Areas of Conservation (SACs) across Wales | Offeryn ar gyfer asesu’r llwyth ffosfforws a nitrogen i Ardaloedd Cadwraeth Arbennig (ACA) ledled Cymru
1 | Introduction (Rhagymadrodd) | Language select | Language: | Iaith:
1 | Introduction (Rhagymadrodd) | Language 1 | English | Saesneg
1 | Introduction (Rhagymadrodd) | Language 2 | Cymraeg | Cymraeg
1 | Introduction (Rhagymadrodd) | Acknowledgements | Contains public sector information licensed under the Open Government Licence v3.0. | Yn cynnwys gwybodaeth sector cyhoeddus a drwyddedwyd dan Drwydded Llywodraeth Agored v3.0.
2 | Background (Cefndir) | Title | Background to nutrient neutrality and the budget calculator | Cefndir i niwtraliaeth maetholion a chyfrifiannell y gyllideb
2 | Background (Cefndir) | Subtitle 1 | What is nutrient neutrality? | Beth yw niwtraliaeth maetholion?
2 | Background (Cefndir) | Text 1 | The 2018 ruling in the European Court of Justice referred to as ‘The Dutch Case’ should be applied to plans or projects that may generate additional nutrient inputs in the catchments of European designated sites (hereafter referred to as Protected sites) that are failing to meet their conservation objectives because of pre-existing levels of nutrients. A key point set out by the Court was that where the condition of a designated habitat is unfavourable, the possibility of authorising further activities which will add additional nutrient loading is ‘necessarily limited’ | Dylid cymhwyso dyfarniad 2018 yn Llys Cyfiawnder Ewrop y cyfeirir ato fel 'Achos yr Iseldiroedd' ar gyfer cynlluniau neu brosiectau a allai gynhyrchu mewnbynnau maetholion ychwanegol yn nalgylchoedd safleoedd dynodedig Ewropeaidd (y cyfeirir atynt o hyn ymlaen fel Safleoedd Gwarchodedig) sy'n methu â bodloni. eu hamcanion cadwraeth oherwydd lefelau maetholion sy'n bodoli eisoes. Pwynt allweddol a nodwyd gan y Llys oedd, lle mae cyflwr cynefin dynodedig yn anffafriol, bod y posibilrwydd o awdurdodi gweithgareddau pellach a fydd yn ychwanegu llwyth maetholion ychwanegol yn ‘angenrheidiol o gyfyngedig’.
2 | Background (Cefndir) | Text 2 | Nutrient neutrality is required where a plan or project could increase the amount of phosphorus in a river SAC and water quality targets for phosphorus are already being exceeded or are failing to meet the targets downstream. In some cases, developments involving new connections to a public sewer will not need to demonstrate nutrient neutrality. Effluent discharges from the associated wastewater treatment works will have been assessed in terms of meeting local water quality targets and are regulated by Natural Resources Wales (NRW) through the works Environmental Permit. | Mae angen niwtraliaeth maetholion lle gallai cynllun neu brosiect gynyddu faint o ffosfforws mewn ACA afon ac mae targedau ansawdd dŵr ar gyfer ffosfforws eisoes yn cael eu rhagori neu'n methu â chyrraedd y targedau i lawr yr afon. Mewn rhai achosion, ni fydd angen i ddatblygiadau sy'n ymwneud â chysylltiadau newydd â charthffos gyhoeddus ddangos niwtraliaeth maetholion. Bydd gollyngiadau elifiant o'r gwaith trin dŵr gwastraff cysylltiedig wedi'u hasesu o ran cyrraedd targedau ansawdd dŵr lleol a chânt eu rheoleiddio gan Cyfoeth Naturiol Cymru (CNC) drwy Drwydded Amgylcheddol y gwaith. | needs translating (word residential removed)
2 | Background (Cefndir) | Text 3 | Habitats Regulations Assessments (HRAs) of new developments need to consider whether nutrient loading will result in ‘Likely Significant Effects’ (LSE) on a protected site. If an HRA finds LSE due to nutrient loading, the Appropriate Assessment will need to consider whether this nutrient load can be mitigated in order to avoid adverse effects on the integrity of the protected site. | Mae angen i Asesiadau Rheoliadau Cynefinoedd (HRAs) o ddatblygiadau newydd ystyried a fydd llwytho maetholion yn arwain at 'Effeithiau Sylweddol Tebygol' (LSE) ar safle gwarchodedig. Os yw HRA yn dod o hyd i LSE oherwydd llwytho maetholion, bydd angen i'r Asesiad Priodol ystyried a ellir lliniaru'r llwyth maetholion hwn er mwyn osgoi effeithiau andwyol ar gyfanrwydd y safle gwarchodedig. | needs translating (word residential removed)
2 | Background (Cefndir) | Text 4 | The first step in an HRA involving nutrient neutrality is understanding both whether a development will need mitigation to achieve nutrient neutrality and, if so, the amount of nutrients that require mitigating on an annual basis. In order to understand the amount of nutrients a new development will create, a nutrient budget is required. | Y cam cyntaf mewn HRA sy'n cynnwys niwtraliaeth maetholion yw deall a fydd angen lliniaru datblygiad i gyflawni niwtraliaeth maethol ac, os felly, faint o faetholion sydd angen lliniaru yn flynyddol. Er mwyn deall faint o faetholion y bydd datblygiad newydd yn eu creu, mae angen cyllideb faetholion. | needs translating (word residential removed)
2 | Background (Cefndir) | Text 5 | The River Usk SAC is partly within Blaenau Gwent, Monmouthshire, Newport, Powys, Torfaen. If a development is within these catchments, a nutrient budget will need to be completed in order to determine if the site will result in 'adverse effects on site integrity' in these protected sites due to an increase in nutrient loading caused by the development. | Mae ACA Afon Wysg yn rhannol o fewn Blaenau Gwent, Sir Fynwy, Casnewydd, Powys, Torfaen. Os yw datblygiad o fewn y dalgylchoedd hyn, bydd angen cwblhau cyllideb faetholion er mwyn penderfynu a fydd y safle'n arwain at 'effeithiau andwyol ar gyfanrwydd y safle' yn y safleoedd gwarchodedig hyn oherwydd cynnydd mewn llwytho maetholion a achosir gan y datblygiad.
2 | Background (Cefndir) | Subtitle 2 | What is this purpose of this calculator and does a nutrient budget need calculating? | Beth yw pwrpas y cyfrifiannell hon ac a oes angen cyfrifo cyllideb faetholion?
2 | Background (Cefndir) | Text 6 | This tool is for anyone who needs to complete a nutrient budget calculation to support an appropriate assessment for the development of residential, commercial, leisure, tourism or public service infrastructure in the River Usk catchment. The tool is primarily aimed at developers who need to complete a nutrient budget calculation to support a planning application and any LPA that needs to understand the mitigation requirements for future development or assess planning applications. It could also be used by communities or environmental groups wanting to understand the impacts of a local development on the nutrient inputs to the sites of concern. The key factors to consider when assessing whether the nutrient neutrality approach is required for a new development are: 1. Whether the development is within a catchment that drains to an affected protected site. 2. Whether the receiving Wastewater Treatment Works discharges to an affected protected site. 3. Whether the development will lead to an increase in ‘overnight stays’. 4. Whether the development will lead to an increase in the number of customers/users or employees coming into the catchment of the SAC river from outside of the catchment to work (in this context a user is defined as a person who may use a service or facilities provided by the development without being directly considered as a customer). If the answer is yes to either 1, or the answer is yes to 2 and 3 or 2 and 4 as outlined above, a nutrient budget calculator will need to be completed in order to assess whether development will increase nutrient loading to a protected site. If unsure whether the development is within a catchment that drains to an affected protected site, the site postcode can be entered into the tool on the ‘Dechrau (Start)’ worksheet, otherwise please follow the guidance. If unsure whether the receiving wastewater treatment works (WwTW) drains to a protected site, please check if the WwTW is in the dropdown list in Stage 1 of the calculator. An increase in overnight stays is defined as any development that will increase the number of people that will stay overnight compared to the previous land use on the development area. Small commercial developments are unlikely to increase the number of employees travelling into the catchment. Estimating the number of employees coming from outside of the catchment may require the assistance of a professional consultancy. | Mae’r offeryn hwn ar gyfer unrhyw un sydd angen cwblhau cyfrifiad cyllideb faetholion i gefnogi asesiad priodol ar gyfer datblygu seilwaith preswyl, masnachol, hamdden, twristiaeth neu wasanaeth cyhoeddus yn nalgylch Afon Wysg. Mae’r offeryn wedi’i anelu’n bennaf at ddatblygwyr sydd angen cwblhau cyfrifiad cyllideb faetholion i gefnogi cais cynllunio ac unrhyw ACLl sydd angen deall y gofynion lliniaru ar gyfer datblygiad yn y dyfodol neu asesu ceisiadau cynllunio. Gallai hefyd gael ei ddefnyddio gan gymunedau neu grwpiau amgylcheddol sydd am ddeall effeithiau datblygiad lleol ar fewnbynnau maetholion i'r safleoedd sy'n peri pryder. Y ffactorau allweddol i'w hystyried wrth asesu a oes angen y dull niwtraliaeth maetholion ar gyfer a datblygiadau newydd yw: 1. A yw'r datblygiad o fewn dalgylch sy'n draenio i safle gwarchodedig yr effeithir arno. 2. A yw'r Gwaith Trin Dŵr Gwastraff sy'n cael ei dderbyn yn gollwng i safle gwarchodedig yr effeithir arno. 3. A fydd y datblygiad yn arwain at gynnydd mewn ‘arosiadau dros nos’. 4. A fydd y datblygiad yn arwain at gynnydd yn nifer y cwsmeriaid/defnyddwyr neu weithwyr sy'n dod i mewn i ddalgylch yr afon ACA o'r tu allan i'r dalgylch i weithio (yn y cyd-destun hwn diffinnir defnyddiwr fel person a all ddefnyddio gwasanaeth neu gyfleusterau a ddarperir gan y datblygiad heb gael eu hystyried yn uniongyrchol fel cwsmer). Os mai ‘ydw’ yw’r ateb i naill ai 1, neu os mai ‘ydw’ yw’r ateb i 2 a 3 neu 2 a 4 fel yr amlinellir uchod, bydd angen cwblhau cyfrifiannell cyllideb faetholion er mwyn asesu a fydd datblygiad yn cynyddu llwyth maethynnau i safle gwarchodedig. Os ydych yn ansicr a yw’r datblygiad o fewn dalgylch sy’n draenio i safle gwarchodedig yr effeithir arno, gellir rhoi cod post y safle yn yr offeryn ar y daflen waith ‘Dechrau (Cychwyn)’, fel arall dilynwch y canllawiau. Os nad ydych yn siŵr a yw’r gwaith trin dŵr gwastraff derbyn yn draenio i safle gwarchodedig, gwiriwch a yw’r GTDG yn y gwymplen yng Ngham 1 y gyfrifiannell. Diffinnir cynnydd mewn arosiadau dros nos fel unrhyw ddatblygiad a fydd yn cynyddu nifer y bobl a fydd yn aros dros nos o gymharu â’r defnydd tir blaenorol ar yr ardal ddatblygu. Mae datblygiadau masnachol bach yn annhebygol o gynyddu nifer y gweithwyr sy'n teithio i'r dalgylch. Efallai y bydd amcangyfrif nifer y gweithwyr sy'n dod o'r tu allan i'r dalgylch yn gofyn am gymorth ymgynghoriaeth broffesiynol.
1 | Instructions (Cyfarwyddiadau) |  | This calculator was created by Ricardo Energy and Environment and Arup. | Crëwyd y gyfrifiannell hon gan Ricardo Energy and Environment ac Arup.
1 | Instructions (Cyfarwyddiadau) |  | This calculator contains 6 worksheets with 11 tables in total. | Mae'r gyfrifiannell hon yn cynnwys 6 taflen waith gyda chyfanswm o 11 tabl.
1 | Instructions (Cyfarwyddiadau) |  | This is the instructions cover sheet. It tells you how to use the calculator and gives an overview of each worksheet. | Dyma ddalen glawr y cyfarwyddiadau. Mae'n dweud wrthych sut i ddefnyddio'r gyfrifiannell ac yn rhoi trosolwg o bob taflen waith.
1 | Instructions (Cyfarwyddiadau) |  | You can move between worksheets using the tabs at the bottom of the page. | Gallwch symud rhwng taflenni gwaith gan ddefnyddio'r tabiau ar waelod y dudalen.
1 | Instructions (Cyfarwyddiadau) |  | If you use screen reading software, you can use 'Ctrl' + 'Page Down' keys to move between the tabs. | Os ydych yn defnyddio meddalwedd darllen sgrin, gallwch ddefnyddio bysellau 'Ctrl' + 'Page Down' i symud rhwng y tabiau.
1 | Instructions (Cyfarwyddiadau) |  | If you use a keyboard only, to open any link in this form first select the cell with the link and then press the 'Shift' + 'F10' keys or the 'Fn' + the 'Menu' keys, then press the letter 'O' twice to highlight 'Open Hyperlink' and press 'Enter'. | Os ydych yn defnyddio bysellfwrdd yn unig, i agor unrhyw ddolen yn y ffurflen hon yn gyntaf dewiswch y gell gyda'r ddolen ac yna pwyswch y bysellau 'Shift' + 'F10' neu'r bysellau 'Fn' + 'Dewislen', yna pwyswch y llythyren ' O' ddwywaith i amlygu 'Open Hyperlink' a gwasgwch 'Enter'.
1 | Instructions (Cyfarwyddiadau) |  | If you use a keyboard only, access dropdown lists by clicking the dropdown arrow or pressing the 'Alt' + 'Down' keys when the cell is selected. | Os ydych yn defnyddio bysellfwrdd yn unig, cyrchwch restrau cwymplen trwy glicio ar y saeth cwymplen neu wasgu'r bysellau 'Alt' + 'Down' pan ddewisir y gell.
1 | Instructions (Cyfarwyddiadau) |  | Table of Contents | Tabl Cynnwys
1 | Instructions (Cyfarwyddiadau) |  | Topic of each worksheet
1 | Instructions (Cyfarwyddiadau) |  | Stage 1: Additional nutrient loading from wastewater
1 | Instructions (Cyfarwyddiadau) |  | Stage 2: Nutrient loading from pre-existing landcovers
1 | Instructions (Cyfarwyddiadau) |  | Stage 3: Nutrient loading from new landcovers being developed
2 | Instructions (Cyfarwyddiadau) |  | Stage 3S: Nutrient load removed through SuDS
3 | Instructions (Cyfarwyddiadau) |  | Stage 4: Final nutrient budget
4 | Instructions (Cyfarwyddiadau)
5 | Instructions (Cyfarwyddiadau)
6 | Instructions (Cyfarwyddiadau)
7 | Instructions (Cyfarwyddiadau)
8 | Instructions (Cyfarwyddiadau)
9 | Instructions (Cyfarwyddiadau)
10 | Instructions (Cyfarwyddiadau)
11 | Instructions (Cyfarwyddiadau)
12 | Instructions (Cyfarwyddiadau)
13 | Instructions (Cyfarwyddiadau)
3 | Instructions (Cyfarwyddiadau) | Title | Instructions - how to use the tool | Cyfarwyddiadau - sut i ddefnyddio'r offeryn
3 | Instructions (Cyfarwyddiadau) | Subtitle 1 | Overview | Trosolwg
3 | Instructions (Cyfarwyddiadau) | Text 1 | To calculate the nutrient loading to a protected site, the user will need to navigate this tool in the order of the four stages of the nutrient budget: | I gyfrifo'r llwyth maetholion i safle gwarchodedig, bydd angen i'r defnyddiwr lywio'r offeryn hwn yn nhrefn pedwar cam y gyllideb faetholion:
3 | Instructions (Cyfarwyddiadau) | Diagram heading 1 | Stage 1 | Cam 1
3 | Instructions (Cyfarwyddiadau) | Diagram heading 2 | Stage 2 | Cam 2
3 | Instructions (Cyfarwyddiadau) | Diagram heading 3 | Stage 3 | Cam 3
3 | Instructions (Cyfarwyddiadau) | Diagram heading 4 | Stage 3S | Cam 3S
3 | Instructions (Cyfarwyddiadau) | Diagram heading 5 | Stage 4 | Cam 4
3 | Instructions (Cyfarwyddiadau) | Diagram details 1 | Nutrient loading from additional wastewater | Llwytho maetholion o ddŵr gwastraff ychwanegol
3 | Instructions (Cyfarwyddiadau) | Diagram details 2 | Nutrient loading from current land use | Llwyth maetholion o ddefnydd tir presennol
3 | Instructions (Cyfarwyddiadau) | Diagram details 3 | Nutrient loading from future land use | Llwyth maetholion o ddefnydd tir yn y dyfodol
3 | Instructions (Cyfarwyddiadau) | Diagram details 4 | Nutrient load removed through SuDS | Llwyth maetholion wedi'i dynnu trwy SuDS
3 | Instructions (Cyfarwyddiadau) | Diagram details 5 | Total nutrient budget that requires mitigation | Cyfanswm y gyllideb faetholion y mae angen ei lliniaru
3 | Instructions (Cyfarwyddiadau) | Text 2 | Site-specific information about the development will need to be entered into Stages 1-3S in order for the tool to calculate the nutrient budget in Stage 4. The outputs from each stage of the nutrient budget are used to calculate the budget using the equation shown below: | Bydd angen cofnodi gwybodaeth safle-benodol am y datblygiad yng Nghamau 1-3S er mwyn i'r offeryn gyfrifo'r gyllideb faetholion yng Ngham 4. Defnyddir yr allbynnau o bob cam o'r gyllideb faetholion i gyfrifo'r gyllideb gan ddefnyddio'r hafaliad a ddangosir isod:
3 | Instructions (Cyfarwyddiadau) | Text 3 | The user must choose the type of development in the 'Project type' user input in the 'Cam 1 (Stage 1)' worksheet. It is essential that the user enters the user inputs in the language that was selected in the Introduction page. If a different language is selected to the language of the inputs the calculator will not function correctly. | Rhaid i'r defnyddiwr ddewis y math o ddatblygiad yn y mewnbwn defnyddiwr 'Math o Brosiect' yn y daflen waith 'Cam 1 (Cam 1)'. Mae'n hanfodol bod y defnyddiwr yn mewnbynnu'r mewnbynnau defnyddiwr yn yr iaith a ddewiswyd ar y dudalen Cyflwyniad. Os dewisir iaith wahanol i iaith y mewnbynnau ni fydd y gyfrifiannell yn gweithio'n gywir.
3 | Instructions (Cyfarwyddiadau) | Subtitle 2 | Basic instructions | Cyfarwyddiadau sylfaenol
3 | Instructions (Cyfarwyddiadau) |  | https://www.gov.wales/find-your-local-planning-authority | https://www.gov.wales/find-your-local-planning-authority
3 | Instructions (Cyfarwyddiadau) |  | https://www.gov.wales/habitats-regulations-assessments-protecting-european-site-html | https://www.llyw.cymru/asesiadau-rheoliadau-cynefinoedd-diogelu-safle-ewropeaidd-html
3 | Instructions (Cyfarwyddiadau) |  | The total phosphorus (TP) and total nitrogen nutrient (TN) budget is calculated automatically once all required inputs have been entered into Stage 1, Stage 2, Stage 3, and Stage 3S (if applicable). The calculation involves adding the values from Stage 1 and the result of Stage 3 subtract Stage 3S (if applicable), and then subtracting the values from the Stage 2. A 20% precautionary buffer is then added to the result. This calculation is completed automatically in the Stage 4 worksheet. | Mae cyfanswm y gyllideb ffosfforws (TP) a chyfanswm maetholion nitrogen (TN) yn cael eu cyfrifo'n awtomatig unwaith y bydd yr holl fewnbynnau gofynnol wedi'u nodi yng Ngham 1, Cam 2, Cam 3, a Cham 3S (os yw'n berthnasol). Mae'r cyfrifiad yn cynnwys adio'r gwerthoedd o Gam 1 a chanlyniad Cam 3 tynnu Cam 3S (os yw'n berthnasol), ac yna tynnu'r gwerthoedd o Gam 2. Yna mae byffer rhagofalus o 20% yn cael ei ychwanegu at y canlyniad. Cwblheir y cyfrifiad hwn yn awtomatig ar daflen waith Cam 4.
3 | Instructions (Cyfarwyddiadau)
3 | Instructions (Cyfarwyddiadau)
3 | Instructions (Cyfarwyddiadau)
3 | Instructions (Cyfarwyddiadau)
3 | Instructions (Cyfarwyddiadau)
3 | Instructions (Cyfarwyddiadau) | Text 3 | When a cell is selected, instructions are shown on how to fill out the cell. These input messages can be moved by clicking and dragging to another location. These pop-up instructions are shown below: | Pan ddewisir cell, dangosir cyfarwyddiadau ar sut i lenwi'r gell. Gellir symud y negeseuon mewnbwn hyn trwy glicio a llusgo i leoliad arall. Dangosir y cyfarwyddiadau naid hyn isod:
3 | Instructions (Cyfarwyddiadau) | Text 4 | When using this tool, it is recommended that you save a new copy of this workbook for each nutrient budget calculation, in order to retain a default blank copy. It may also be useful to open two calculators with one showing the instructions and one showing the calculator. | Wrth ddefnyddio'r offeryn hwn, argymhellir bod y defnyddiwr yn arbed copi newydd o'r llyfr gwaith hwn ar gyfer pob cyfrifiad cyllideb faetholion, er mwyn cadw copi gwag rhagosodedig. Gall fod yn ddefnyddiol hefyd agor dwy gyfrifiannell gydag un yn dangos y cyfarwyddiadau ac un yn dangos y gyfrifiannell.
3 | Instructions (Cyfarwyddiadau) | Text 5 | The pre-populated values in this calculator have been identified through extensive research and modelling. The values are based on the best available evidence and are suitably precautionary to account for any uncertainty. This nutrient budget calculator can be used as supporting evidence for a Habitat Regulations Assessment (HRA). Specifically, this calculator can be used within an appropriate assessment to assess the likely significant effects of a proposal on the integrity of the site and its conservation objectives. It is highly unadvisable to edit the values in this tool without a sufficient evidence base to justify any changes. | Mae'r gwerthoedd a ragboblogwyd yn y gyfrifiannell hon wedi'u nodi trwy waith ymchwil a modelu helaeth. Mae'r gwerthoedd yn seiliedig ar y dystiolaeth orau sydd ar gael ac maent yn ddigon rhagofalus i roi cyfrif am unrhyw ansicrwydd. Gellir defnyddio'r gyfrifiannell cyllideb faetholion hon fel tystiolaeth ategol ar gyfer Asesiadau Rheoliadau Cynefinoedd (HRA). Yn benodol, gellir defnyddio'r gyfrifiannell hon o fewn asesiad priodol i asesu effeithiau sylweddol tebygol cynnig ar gyfanrwydd y safle a'i amcanion cadwraeth. Mae'n annoeth iawn golygu'r gwerthoedd yn yr offeryn hwn heb sylfaen dystiolaeth ddigonol i gyfiawnhau unrhyw newidiadau.
3 | Instructions (Cyfarwyddiadau) | Heading 1 | Stage specific instructions | Cyfarwyddiadau cam-benodol
3 | Instructions (Cyfarwyddiadau) | Subheading 1 | Start sheet: | Taflen gychwyn
3 | Instructions (Cyfarwyddiadau) | Text 6 | This section is used to enter key information about the development for clarity. In addition, there is a function that allows the user to find their LPA and their rainfall is their site is within the catchment of an affected Protected site. Entering the postcode for the site, or the nearest postcode, will generate estimated site information that can be used to initially assist the user. However, it is the responsibility of the user to confirm this information is correct. | Defnyddir yr adran hon i fewnbynnu gwybodaeth allweddol am y datblygiad er mwyn eglurder. Yn ogystal, mae yna swyddogaeth sy'n caniatáu i'r defnyddiwr ddod o hyd i'w LPA a'u glawiad yw bod eu safle o fewn dalgylch safle Gwarchodedig yr effeithir arno. Bydd nodi cod post y safle, neu'r cod post agosaf, yn cynhyrchu gwybodaeth amcangyfrifedig am y safle y gellir ei defnyddio i gynorthwyo'r defnyddiwr i ddechrau. Fodd bynnag, cyfrifoldeb y defnyddiwr yw cadarnhau bod y wybodaeth hon yn gywir.
3 | Instructions (Cyfarwyddiadau) | Subheading 2 | Stage 1 - calculate the new nutrient load associated with the additional wastewater: | Cam 1 - cyfrifwch y llwyth maetholion newydd sy'n gysylltiedig â'r dŵr gwastraff ychwanegol:
3 | Instructions (Cyfarwyddiadau) | Text 7 | In this section the user will need to: > Select the development type from the dropdown list. This option changes the inputs required for Stage 1. The details of how the planning permission use classes have been categorised into the development types can be found in the 'Digrifiadau (Descriptions)' worksheet. > Enter the appropriate local planning authority (LPA) for the development if the postcode lookup function in the 'Dechrau (Start)' has not been used or has not returned a value. > For residential developments, the user must enter the average occupancy rate of the development. The default setting is the average for the LPA. The units are people per dwelling/unit. Only change this value if there is sufficient evidence that the development will be different to this value. > For all other developments, the user must enter the number of users and employees per unit, as well as the percentage of users and employees that come into the catchment from outside of the catchment. > Enter the estimated average water usage per person. This is set to a default of 120 litres/person/day which is 10 litres higher than the standard set by the Welsh Ministers of 110 litres/person/day of wholesome water where a dwelling/unit is erected. The extra 10 litres is a precautionary approach to account for water usage variations. If a dwelling/unit is formed by a material change of use of a building, then this value should be changed to 135 litres/person/day. Again, this value is 10 litres/person/day above the Building Regulations standard of 125 litres/person/day in order to be precautionary for the same reasons identified above. > Enter the number of dwellings/units that will comprise the development at the time of project completion. > Enter the Wastewater Treatment Works (WwTW) to which the development will drain. If the WwTW the site will drain to is not known, please obtain this information from Dwr Cymru/Welsh Water in order to complete the calculator. If connecting to the sewerage network is unfeasible and a septic tank or package treatment plant is being used, please select this option. Please be aware that if total phosphorus (TP) final effluent concentrations (in mg/l) are specified by the manufacturer, please select 'Septic Tank user defined' or 'Package Treatment Plant user defined' and enter the manufacturer specified value in the cell where prompted. The WwTW are correct at the time of publication but may be subject to change in the future. If required, these values will be updated at a later date accordingly. The potential for changing permits is the reason for there being two values for nutrient permits in the lookup table. | Yn yr adran hon bydd angen i'r defnyddiwr: > Dewiswch y math o ddatblygiad o'r gwymplen. Mae'r opsiwn hwn yn newid y mewnbynnau sydd eu hangen ar gyfer Cam 1. Mae manylion sut mae dosbarthiadau defnydd caniatâd cynllunio wedi eu categoreiddio i'r mathau o ddatblygiad i'w gweld yn y daflen waith 'Disgrifiadau (Descriptions)'. > Nodwch yr awdurdod cynllunio lleol (ACLl) priodol ar gyfer y datblygiad os nad yw'r swyddogaeth chwilio cod post yn y 'Dechrau (Start)' wedi'i defnyddio neu os nad yw wedi dychwelyd gwerth. > Ar gyfer datblygiadau preswyl, rhaid i'r defnyddiwr nodi cyfradd deiliadaeth gyfartalog y datblygiad. Y gosodiad diofyn yw'r cyfartaledd ar gyfer yr LPA. Pobl fesul annedd/uned yw'r unedau. Newidiwch y gwerth hwn dim ond os oes digon o dystiolaeth y bydd y datblygiad yn wahanol i'r gwerth hwn. > Ar gyfer pob datblygiad arall, rhaid i'r defnyddiwr nodi nifer y defnyddwyr a'r gweithwyr fesul uned, yn ogystal â chanran y defnyddwyr a'r gweithwyr sy'n dod i'r dalgylch o'r tu allan i'r dalgylch. > Nodwch amcangyfrif o'r defnydd dŵr cyfartalog fesul person. Mae hyn wedi’i osod i ddiofyn o 120 litr/person/dydd sydd 10 litr yn uwch na’r safon a osodwyd gan Weinidogion Cymru o 110 litr/person/diwrnod o ddŵr iachusol pan godir annedd/uned. Mae'r 10 litr ychwanegol yn ddull rhagofalus o roi cyfrif am amrywiadau yn y defnydd o ddŵr. Os yw annedd/uned yn cael ei ffurfio drwy newid defnydd materol adeilad, yna dylid newid y gwerth hwn i 135 litr/person/dydd. Eto, mae'r gwerth hwn 10 litr/person/dydd yn uwch na safon Rheoliadau Adeiladu o 125 litr/person/dydd er mwyn bod yn rhagofalus am yr un rhesymau a nodir uchod. > Nodwch nifer yr anheddau/unedau a fydd yn rhan o'r datblygiad ar adeg cwblhau'r prosiect. > Mynd i mewn i'r Gwaith Trin Dŵr Gwastraff y bydd y datblygiad yn draenio iddo. Os nad yw’r GTDG y bydd y safle’n draenio iddo yn hysbys, gofynnwch am y wybodaeth hon gan Dŵr Cymru/Welsh Water er mwyn cwblhau’r gyfrifiannell. Os yw cysylltu â'r rhwydwaith carthffosiaeth yn anymarferol a bod tanc septig neu offer trin pecyn yn cael ei ddefnyddio, dewiswch yr opsiwn hwn. Sylwch, os yw cyfanswm crynodiadau elifiant terfynol ffosfforws (TP) (mewn mg/l) wedi'u pennu gan y gwneuthurwr, dewiswch 'Diffiniwyd gan y Defnyddiwr Tanc Septig' neu 'Diffiniwyd gan Ddefnyddiwr Pecyn Triniaeth Defnyddiwr' a nodwch werth penodedig y gwneuthurwr yn y gell. lle ysgogwyd. Y GTDG yn gywir ar adeg cyhoeddi ond efallai y byddant yn newid yn y dyfodol. Os bydd angen, caiff y gwerthoedd hyn eu diweddaru yn ddiweddarach yn unol â hynny. Y potensial ar gyfer newid trwyddedau yw'r rheswm pam fod dau werth ar gyfer trwyddedau maetholion yn y tabl chwilio.
|  |  | > Select the development type from the dropdown list. This option changes the inputs required for Stage 1. The details of how the planning permission use classes have been categorised into the development types can be found in the 'Digrifiadau (Descriptions)' worksheet. | > Dewiswch y math o ddatblygiad o'r gwymplen. Mae'r opsiwn hwn yn newid y mewnbynnau sydd eu hangen ar gyfer Cam 1. Mae manylion sut mae dosbarthiadau defnydd caniatâd cynllunio wedi eu categoreiddio i'r mathau o ddatblygiad i'w gweld yn y daflen waith 'Disgrifiadau (Descriptions)'.
3 | Instructions (Cyfarwyddiadau) | Text 8 | > Enter the appropriate local planning authority (LPA) for the development if the postcode lookup function in the 'Dechrau (Start)' has not been used or has not returned a value. | > Nodwch yr awdurdod cynllunio lleol (ACLl) priodol ar gyfer y datblygiad os nad yw'r swyddogaeth chwilio cod post yn y 'Dechrau (Start)' wedi'i defnyddio neu os nad yw wedi dychwelyd gwerth.
3 | Instructions (Cyfarwyddiadau) | Text 9 | > For residential developments, the user must enter the average occupancy rate of the development. The default setting is the average for the LPA. The units are people per dwelling/unit. Only change this value if there is sufficient evidence that the development will be different to this value. > For all other developments, the user must enter the number of users and employees per unit, as well as the percentage of users and employees that come into the catchment from outside of the catchment. | > Ar gyfer datblygiadau preswyl, rhaid i'r defnyddiwr nodi cyfradd deiliadaeth gyfartalog y datblygiad. Y gosodiad diofyn yw'r cyfartaledd ar gyfer yr LPA. Pobl fesul annedd/uned yw'r unedau. Newidiwch y gwerth hwn dim ond os oes digon o dystiolaeth y bydd y datblygiad yn wahanol i'r gwerth hwn. > Ar gyfer pob datblygiad arall, rhaid i'r defnyddiwr nodi nifer y defnyddwyr a'r gweithwyr fesul uned, yn ogystal â chanran y defnyddwyr a'r gweithwyr sy'n dod i'r dalgylch o'r tu allan i'r dalgylch.
3 | Instructions (Cyfarwyddiadau) | Text 10 | > Enter the estimated average water usage per person. This is set to a default of 120 litres/person/day which is 10 litres higher than the standard set by the Welsh Ministers of 110 litres/person/day of wholesome water where a dwelling/unit is erected. The extra 10 litres is a precautionary approach to account for water usage variations. If a dwelling/unit is formed by a material change of use of a building, then this value should be changed to 135 litres/person/day. Again, this value is 10 litres/person/day above the Building Regulations standard of 125 litres/person/day in order to be precautionary for the same reasons identified above. | > Nodwch amcangyfrif o'r defnydd dŵr cyfartalog fesul person. Mae hyn wedi’i osod i ddiofyn o 120 litr/person/dydd sydd 10 litr yn uwch na’r safon a osodwyd gan Weinidogion Cymru o 110 litr/person/diwrnod o ddŵr iachusol pan godir annedd/uned. Mae'r 10 litr ychwanegol yn ddull rhagofalus o roi cyfrif am amrywiadau yn y defnydd o ddŵr. Os yw annedd/uned yn cael ei ffurfio drwy newid defnydd materol adeilad, yna dylid newid y gwerth hwn i 135 litr/person/dydd. Eto, mae'r gwerth hwn 10 litr/person/dydd yn uwch na safon Rheoliadau Adeiladu o 125 litr/person/dydd er mwyn bod yn rhagofalus am yr un rhesymau a nodir uchod.
3 | Instructions (Cyfarwyddiadau) | Text 11 | > Enter the number of dwellings/units that will comprise the development at the time of project completion. | > Nodwch nifer yr anheddau/unedau a fydd yn rhan o'r datblygiad ar adeg cwblhau'r prosiect.
3 | Instructions (Cyfarwyddiadau) | Text 12 | > Enter the Wastewater Treatment Works (WwTW) to which the development will drain. If the WwTW the site will drain to is not known, please obtain this information from Dwr Cymru/Welsh Water in order to complete the calculator. If connecting to the sewerage network is unfeasible and a septic tank or package treatment plant is being used, please select this option. Please be aware that if total phosphorus (TP) final effluent concentrations (in mg/l) are specified by the manufacturer, please select 'Septic Tank user defined' or 'Package Treatment Plant user defined' and enter the manufacturer specified value in the cell where prompted. The WwTW are correct at the time of publication but may be subject to change in the future. If required, these values will be updated at a later date accordingly. The potential for changing permits is the reason for there being two values for nutrient permits in the lookup table. | > Mynd i mewn i'r Gwaith Trin Dŵr Gwastraff y bydd y datblygiad yn draenio iddo. Os nad yw’r GTDG y bydd y safle’n draenio iddo yn hysbys, gofynnwch am y wybodaeth hon gan Dŵr Cymru/Welsh Water er mwyn cwblhau’r gyfrifiannell. Os yw cysylltu â'r rhwydwaith carthffosiaeth yn anymarferol a bod tanc septig neu offer trin pecyn yn cael ei ddefnyddio, dewiswch yr opsiwn hwn. Sylwch, os yw cyfanswm crynodiadau elifiant terfynol ffosfforws (TP) (mewn mg/l) wedi'u pennu gan y gwneuthurwr, dewiswch 'Diffiniwyd gan y Defnyddiwr Tanc Septig' neu 'Diffiniwyd gan Ddefnyddiwr Pecyn Triniaeth Defnyddiwr' a nodwch werth penodedig y gwneuthurwr yn y gell. lle ysgogwyd. Y GTDG yn gywir ar adeg cyhoeddi ond efallai y byddant yn newid yn y dyfodol. Os bydd angen, caiff y gwerthoedd hyn eu diweddaru yn ddiweddarach yn unol â hynny. Y potensial ar gyfer newid trwyddedau yw'r rheswm pam fod dau werth ar gyfer trwyddedau maetholion yn y tabl chwilio.
3 | Instructions (Cyfarwyddiadau) | Subheading 3 | Stage 2 - calculate the annual nutrient load from existing (pre-development) land use on the development site: | Cam 2 - cyfrifo’r llwyth maetholion blynyddol o ddefnydd tir presennol (cyn datblygu) ar y safle datblygu:
3 | Instructions (Cyfarwyddiadau) | Text 13 | In this section some environmental information about the development will need to be entered as well as the type(s) and area(s) of landcover on the development site. Only landcovers for the land that is being altered by the development should be entered. | Yn yr adran hon bydd angen nodi rhywfaint o wybodaeth amgylcheddol am y datblygiad yn ogystal â'r math(au) a'r ardal(oedd) o orchudd tir ar safle'r datblygiad. Dim ond gorchuddion tir ar gyfer y tir sy'n cael ei addasu gan y datblygiad y dylid mynd i mewn iddo.
3 | Instructions (Cyfarwyddiadau) | Text 14 | Before selecting the landcover types, the user must first enter the drainage associated with the predominant soil type within the development site and the average annual rainfall volume. | Cyn dewis y mathau o orchudd tir, yn gyntaf rhaid i'r defnyddiwr fynd i mewn i'r draeniad sy'n gysylltiedig â'r prif fath o bridd o fewn y safle datblygu a'r cyfaint glawiad blynyddol cyfartalog.
3 | Instructions (Cyfarwyddiadau) | Text 15 | Instructions on how to find the soil drainage information: | Cyfarwyddiadau ar sut i ddod o hyd i'r wybodaeth draenio pridd
3 | Instructions (Cyfarwyddiadau) | Text 16 | a) Go to this link: | a) Ewch i'r ddolen hon:
3 | Instructions (Cyfarwyddiadau) | Link 1 | http://www.landis.org.uk/soilscapes/#. | http://www.landis.org.uk/soilscapes/# .
3 | Instructions (Cyfarwyddiadau) | Text 17 | b) Find the site location on the map by using the search bar on the right side of the map in the 'Search' tab. Searching an area will generate a pop up window in which you can view the soil information by clicking 'View soil information'. If this is not an option then click on the relevant soil type on the map and click on the 'Soil information' tab on the right hand side of the map, below the 'Search' tab. | b) Dewch o hyd i leoliad y safle ar y map trwy ddefnyddio'r bar chwilio ar ochr dde'r map yn y tab 'Chwilio'. Bydd chwilio ardal yn creu ffenestr naid lle gallwch weld y wybodaeth am bridd trwy glicio ar 'Gweld gwybodaeth pridd'. Os nad yw hyn yn opsiwn yna cliciwch ar y math o bridd perthnasol ar y map a chliciwch ar y tab 'Gwybodaeth Pridd' ar ochr dde'r map, o dan y tab 'Chwilio'.
3 | Instructions (Cyfarwyddiadau) | Text 18 | c) The 'Soil drainage type' value can be found In the 'Soil information' under the title 'Drainage:' | c) Mae'r gwerth 'math draeniad pridd' i'w weld yn y 'Pridd Gwybodaeth' o dan y teitl 'Draenio:'
3 | Instructions (Cyfarwyddiadau) | Text 19 | d) Make a note of this soil type and select the relevant soil drainage type from the drop down list in the relevant cell. | d) Gwnewch nodyn o'r math hwn o bridd a dewiswch y math draenio pridd perthnasol o'r gwymplen yn y gell berthnasol.
3 | Instructions (Cyfarwyddiadau) | Text 20 | Instructions on how to find the annual average rainfall that the development will receive: | Cyfarwyddiadau ar sut i ddod o hyd i'r glawiad cyfartalog blynyddol y bydd y datblygiad yn ei gael:
3 | Instructions (Cyfarwyddiadau) | Text 21 | a) Go to this link: | a) Ewch i'r ddolen hon:
3 | Instructions (Cyfarwyddiadau) | Link 2 | https://nrfa.ceh.ac.uk/data/station/info/56001 | https://nrfa.ceh.ac.uk/data/station/info/56001
3 | Instructions (Cyfarwyddiadau) | Text 22 | b) This link will bring the user to the Usk at Chainbridge flow gauge catchment information page (there is no need to change the catchment area to obtain the required information). | b) Bydd y ddolen hon yn dod â’r defnyddiwr i dudalen gwybodaeth dalgylch mesurydd llif afon Wysg yn Chainbridge (nid oes angen newid y dalgylch i gael y wybodaeth ofynnol).
3 | Instructions (Cyfarwyddiadau) | Text 23 | c) Click on the 'Catchment info' tab. Then click the dropdown list next to the title 'Select spatial data type to view:' on the left of the map and select 'Rainfall'. Next select the Legend tab. | c) Cliciwch ar y tab 'Catchinfo'. Yna cliciwch y gwymplen wrth ymyl y teitl 'Dewis math o ddata gofodol i weld:' ar ochr chwith y map a dewiswch 'Rainfall'. Nesaf, dewiswch y tab Legend.
3 | Instructions (Cyfarwyddiadau) | Text 24 | d) Change the tab from Catchment statistics to Legend. Zoom in on the map to find the location of the development and find the corresponding rainfall range by comparing the colour on the map location to the Legend. | d) Newidiwch y tab o ystadegau Dalgylch i Chwedl. Chwyddo i mewn ar y map i ddod o hyd i leoliad y datblygiad a dod o hyd i'r amrediad glawiad cyfatebol trwy gymharu'r lliw ar leoliad y map â'r Allwedd.
3 | Instructions (Cyfarwyddiadau) | Text 25 | e) Select the rainfall band from the drop down list in the table. If your rainfall band is not in the drop down list, please select the closest band shown in the list. | e) Dewiswch y band glawiad o'r gwymplen yn y tabl. Os nad yw eich band glawiad yn y gwymplen, dewiswch y band agosaf a ddangosir yn y rhestr.
3 | Instructions (Cyfarwyddiadau) | Text 26 | The drop down list of landcover types contains ten agricultural landcover types and eight different non-agricultural landcover types that may be present in the development. The ten agricultural landcover types that are selectable in Stage 2 are based on the Defra robust farm types. The descriptions of each landcover type can be found in the 'Disgrifiadau (Descriptions)' worksheet. The guidance document that accompanies this calculator provides some examples of developments and the appropriate landcover type to select. Please find out what landcover types are within the development before completing this tool. If there is a landcover within the development area that is not in the list please select the most similar landcover type. | Mae’r gwymplen o fathau o orchudd tir yn cynnwys deg math o orchudd tir amaethyddol ac wyth math gwahanol o orchudd tir an-amaethyddol a all fod yn bresennol yn y datblygiad. Mae'r deg math o orchudd tir amaethyddol y gellir eu dethol yng Ngham 2 yn seiliedig ar fathau cadarn o ffermydd Defra. Mae disgrifiadau o bob math o orchudd tir i'w gweld yn y daflen waith 'Disgrifiadau (Descriptions)'. Mae'r ddogfen ganllaw sy'n cyd-fynd â'r gyfrifiannell hon yn rhoi rhai enghreifftiau o ddatblygiadau a'r math priodol o orchudd tir i'w ddewis. Darganfyddwch pa fathau o orchudd tir sydd o fewn y datblygiad cyn cwblhau'r offeryn hwn. Os oes gorchudd tir o fewn yr ardal ddatblygu nad yw ar y rhestr dewiswch y math gorchudd tir tebycaf.
3 | Instructions (Cyfarwyddiadau) | Subheading 4 | Stage 3 - calculate the annual nutrient load from new (post-development) land use on the development site: | Cam 3 - cyfrifo’r llwyth maetholion blynyddol o ddefnydd tir newydd (ar ôl datblygu) ar y safle datblygu:
3 | Instructions (Cyfarwyddiadau) | Text 27 | In this section the user will need to select the type(s) and area(s) of the landcover present on the new site. | Yn yr adran hon bydd angen i'r defnyddiwr ddewis y math(au) a'r ardal(oedd) o'r gorchudd tir sy'n bresennol ar y safle newydd.
3 | Instructions (Cyfarwyddiadau) | Text 28 | The drop down list of landcover types contains eight different landcover types that may be present on the development site. Please find out what landcover types will be within the development site before completing this tool. If there is a landcover within the development site that is not in the list please select the most similar landcover type. | Mae'r gwymplen o fathau o orchudd tir yn cynnwys wyth math gwahanol o orchudd tir a all fod yn bresennol ar y safle datblygu. Darganfyddwch pa fathau o orchudd tir fydd o fewn y safle datblygu cyn cwblhau'r offeryn hwn. Os oes gorchudd tir o fewn y safle datblygu nad yw ar y rhestr dewiswch y math gorchudd tir tebycaf.
3 | Instructions (Cyfarwyddiadau) | Text 29 | The 'Digrifiadau (Descriptions)' worksheet and guidance document provides information on each landcover type. | Mae'r daflen waith a'r ddogfen ganllaw 'Digrifiadau (Descriptions)' yn rhoi gwybodaeth am bob math o orchudd tir.
3 | Instructions (Cyfarwyddiadau) | Subheading 5 | Stage 3S - calculate the annual nutrient load removed from Sustainable Urban Drainage Systems (SuDS): | Cam 3S - cyfrifwch y llwyth maethol blynyddol sy'n cael ei dynnu o Systemau Draenio Cynaliadwy (SuDS):
3 | Instructions (Cyfarwyddiadau) | Text 31 | In this section the user will need to enter information about the SuDS features used to calculate the amount of nutrients removed through SuDS treatment of surface runoff. This section must only be completed if SuDS are compliant with the national standards and are being implemented under the requirement of the Flood and Water Management Act 2010 (Schedule 3). Any SuDS that are being implemented in addition to the site plans for the purposes of mitigation must not be considered in the nutrient budget calculation for the site. In this instance, it is instead recommended that a second calculation is populated - the People over Wind judgment means that it is no longer possible to apply mitigation measures at the screening stage. | Yn yr adran hon bydd angen i’r defnyddiwr fewnbynnu gwybodaeth am y nodweddion SuDS a ddefnyddir i gyfrifo faint o faetholion sy’n cael eu tynnu drwy driniaeth SuDS o ddŵr ffo arwyneb. Rhaid llenwi’r adran hon dim ond os yw SDCau yn cydymffurfio â’r safonau cenedlaethol ac yn cael eu gweithredu o dan ofyniad Deddf Rheoli Llifogydd a Dŵr 2010 (Atodlen 3). Ni ddylai unrhyw SDCau sy'n cael eu gweithredu yn ychwanegol at y cynlluniau safle at ddibenion lliniaru gael eu hystyried wrth gyfrifo cyllideb faetholion y safle. Yn yr achos hwn, argymhellir yn lle hynny y dylid llenwi ail gyfrifiad - mae dyfarniad People over Wind yn golygu nad yw bellach yn bosibl defnyddio mesurau lliniaru yn y cam sgrinio.
3 | Instructions (Cyfarwyddiadau) | Text 32 | The landcovers and areas present on the new site will be automatically populated from Stage 3. | Bydd y gorchuddion tir a’r ardaloedd sy’n bresennol ar y safle newydd yn cael eu poblogi’n awtomatig o Cam 3.
3 | Instructions (Cyfarwyddiadau) | Text 33 | You will need to: - enter the catchment area that drains to the SuDS as a proportion of the new landcovers - choose the SuDS features used - enter the nutrient removal rates as a percentage | Bydd angen i chi: - mynd i mewn i'r dalgylch sy'n draenio i'r SDCau fel cyfran o'r gorchudd tir newydd - dewiswch y nodweddion SuDS a ddefnyddir - nodwch y cyfraddau tynnu maetholion fel canran
3 | Instructions (Cyfarwyddiadau) | Text 34 | It is recommended that the surface area of the SuDS features are included within the area of the landcover that they drain. If required, you can split the landcover up in Stage 3 to demonstrate multiple drainage configurations. You can select a SuDS feature from a list of 23 options. If a SuDS management train that comprises multiple SuDS features is being implemented you should select the appropriate option from the start of the list. Otherwise, you should select the individual SuDS feature being used. If the appropriate SuDS feature cannot be found in the list, select the most relevant alternative. The nutrient removal rates should be entered as a whole number percentage between 0-100. You must be able to provide evidence for the removal rates you have entered. This is likely to require the submission of a drainage assessment and a detailed design of the SuDS features. | Argymhellir bod arwynebedd y nodweddion SuDS yn cael ei gynnwys o fewn ardal y gorchudd tir y maent yn ei ddraenio. Os oes angen, gallwch rannu'r gorchudd tir yng Ngham 3 i ddangos ffurfweddiadau draenio lluosog. Gallwch ddewis nodwedd SDCau o restr o 23 opsiwn. Os yw trên rheoli SDCau sy'n cynnwys nifer o nodweddion SuDS yn cael ei weithredu, dylech ddewis yr opsiwn priodol o ddechrau'r rhestr. Fel arall, dylech ddewis y nodwedd SDCau unigol a ddefnyddir. Os na ellir dod o hyd i'r nodwedd SDCau briodol yn y rhestr, dewiswch y dewis arall mwyaf perthnasol. Dylid nodi'r cyfraddau tynnu maetholion fel canran rhif cyfan rhwng 0-100. Mae'n rhaid i chi allu darparu tystiolaeth ar gyfer y cyfraddau dileu rydych wedi'u nodi. Mae hyn yn debygol o olygu bod angen cyflwyno asesiad draenio a dyluniad manwl o nodweddion SDCau.
3 | Instructions (Cyfarwyddiadau) | Text 35 | The amount of nutrients removed through SuDS is automatically calculated using the landcovers and associated loads from Stage 3, the drainage area, and the nutrient removal rates. The total load removed through SuDS is incorporated into the final nutrient budget calculation. Selecting the type of SuDS feature used is to ensure that the nutrient budget calculator matches the SuDS design detailed in the planning application. | Mae faint o faetholion sy'n cael eu tynnu trwy SuDS yn cael ei gyfrifo'n awtomatig gan ddefnyddio'r tirluniau a'r llwythi cysylltiedig o Gyfnod 3, yr ardal ddraenio, a'r cyfraddau tynnu maetholion. Mae cyfanswm y llwyth sy'n cael ei dynnu trwy SuDS wedi'i ymgorffori yn y cyfrifiad cyllideb faethol terfynol. Mae dewis y math o nodwedd SuDS a ddefnyddir er mwyn sicrhau bod y gyfrifiannell cyllideb faetholion yn cyd-fynd â’r dyluniad SuDS a nodir yn y cais cynllunio.
3 | Instructions (Cyfarwyddiadau) | Text 36 | Sources of information on SuDS and how to design them for nutrient removal | Ffynonellau gwybodaeth am SDCau a sut i'w dylunio i gael gwared ar faetholion
3 | Instructions (Cyfarwyddiadau) | Text 37 | National standards for sustainable drainage systems (SuDS) can be found here: | Safonau cenedlaethol ar gyfer systemau draenio cynaliadwy (SuDS) ar gael yma:
3 | Instructions (Cyfarwyddiadau) | Text 38 | Ciria's Using SuDS to reduce nitrogen in surface water runoff (C815) can be found here: | Mae Ciria's Defnyddio SuDS i leihau nitrogen mewn dŵr ffo wyneb (C815) i'w weld yma:
3 | Instructions (Cyfarwyddiadau) | Text 39 | Ciria's Using SuDS to reduce phosphorus in surface water runoff (C808F) can be found here: | Mae Ciria's yn Defnyddio SuDS i leihau ffosfforws mewn dŵr ffo wyneb (C808F) i'w weld yma:
3 | Instructions (Cyfarwyddiadau) | Link 1 | https://www.gov.wales/national-standards-sustainable-drainage-systems-suds | https://www.llyw.cymru/safonau-cenedlaethol-ar-gyfer-systemau-draenio-cynaliadwy-suds
3 | Instructions (Cyfarwyddiadau) | Link 2 | https://www.ciria.org/CIRIA/Books/Free_publications/C815F.aspx | https://www.ciria.org/CIRIA/Books/Free_publications/C815F.aspx
3 | Instructions (Cyfarwyddiadau) | Link 3 | https://www.ciria.org/CIRIA/CIRIA/Item_Detail.aspx?iProductCode=C808F&Category=FREEPUBS | https://www.ciria.org/CIRIA/CIRIA/Item_Detail.aspx?iProductCode=C808F&Category=FREEPUBS
3 | Instructions (Cyfarwyddiadau) | Subheading 6 | Stage 4 - calculate the final annual nutrient budget for the development site: | Cam 4 - cyfrifo’r gyllideb faetholion flynyddol derfynol ar gyfer y safle datblygu:
3 | Instructions (Cyfarwyddiadau) | Text 40 | This final stage automatically calculates the final nutrient budget using the results from Stage 1 to Stage 3S using the following equation: ((Stage 1 - Stage 2) + (Stage 3 - Stage 3S)) * 1.2 | Mae’r cam olaf hwn yn cyfrifo’r gyllideb faetholion derfynol yn awtomatig gan ddefnyddio’r canlyniadau o Gam 1 i Gam 3S gan ddefnyddio’r hafaliad canlynol: ((Cam 1 - Cam 2) + (Cam 3 - Cam 3S)) * 1.2
3 | Instructions (Cyfarwyddiadau) | Text 41 | The value(s) shown are how much nutrient mitigation is required in kilograms per year to achieve nutrient neutrality. | Y gwerth(oedd) a ddangosir yw faint o liniaru maetholion sydd ei angen mewn cilogramau y flwyddyn i gyflawni niwtraliaeth maetholion.
4 | Start (Dechrau) | Title | Start - enter key information about the project | Cychwyn - rhowch wybodaeth allweddol am y prosiect
4 | Start (Dechrau) | Subtitle 1 | Project details | Manylion y prosiect
4 | Start (Dechrau) | Heading 1 | Project name: | Enw'r prosiect:
4 | Start (Dechrau) | Heading 2 | Project type: | Math o brosiect:
4 | Start (Dechrau) | Heading 3 | Planning application reference: | Cyfeirnod cais cynllunio:
4 | Start (Dechrau) | Heading 4 | Total site area (hectares): | Cyfanswm arwynebedd y safle (hecatrau):
4 | Start (Dechrau) | Heading 5 | Completed by: | Cwblhawyd gan:
4 | Start (Dechrau) | Heading 6 | Date of budget calculation: | Dyddiad cyfrifo’r gyllideb:
4 | Start (Dechrau) | Heading 7 | Address: | Cyfeiriad:
4 | Start (Dechrau) | Subtitle 2 | Postcode search tool | Offeryn chwilio cod post
|  |  | Special Area of Conservation (SAC): | Ardaloedd Cadwraeth Arbennig (ACA):
4 | Start (Dechrau) | Heading 8 | Postcode: | Côd post:
4 | Start (Dechrau) | Heading 9 | Local Planning Authority (LPA): | Awdurdod Cynllunio Lleol (ACLl):
4 | Start (Dechrau) | Heading 10 | Rainfall: | Glawiad:
4 | Start (Dechrau) | Heading 11 | Nearest wastewater treatment works (WwTW): | Gwaith Trin Dŵr Gwastraff Agosaf (GTDG):
4 | Start (Dechrau) | Heading 12 | Distance of nearest WwTW (metres): | Pellter o’r GTDG agosaf (metrau):
4 | Start (Dechrau) | Heading 13 | The postcode you have entered is not within the boundary of the SAC catchment. If the wastewater drains to the SAC via the sewerage network you may still need to complete a nutrient budget calculation. It is recommended that you check whether a nutrient budget calculation is required with your LPA. | Nid yw'r cod post yr ydych wedi'i nodi o fewn ffin y dalgylch ACA. Os yw'r dŵr gwastraff yn draenio i'r ACA drwy'r rhwydwaith carthffosiaeth efallai y bydd angen i chi gwblhau cyfrifiad cyllideb maetholion o hyd. Argymhellir eich bod yn gwirio a oes angen cyfrifiad cyllideb faetholion gyda'ch LPA.
5 | Stage 1 (Cam 1) | Title | Stage 1 - additional nutrient loading from wastewater | Cam 1 - llwytho maetholion ychwanegol o ddŵr gwastraff
|  | A2 text | This sheet contains 3 tables. The tables are separated by a heading, which describes the following table. Note: You may fill in cell B5 in the first table labelled 'Postcode lookup tool'. Cells B6 and B7 are automatically generated. In the second table labelled 'Wastewater load calculation table', you will need to fill in cells B10 to B23. Cells B24 and B25 are automatically generated and will state '0.00' unless the user inputs have been entered. Cells A12 and B12 are automatically generated and will state 'Not applicable' if the user inputs data in the first table labelled 'Postcode lookup tool'. Cells A13 to B14, A17 to B20 and A22 to B23 are automatically generated and will state 'Not applicable' depending on the user inputs to cell B10. You do not need to fill in any cells in the third table labelled 'Final calculation of nutrient load from wastewater'. Cells B28 to B31 are automatically generated and will state '0.00' unless the user inputs have been entered in the second table labelled 'Wastewater load calculation table'. How to fill in the table 'Postcode lookup tool' Cell B5: Enter the postcode or nearest postcode of the proposed development site. The estimated Local planning authority is automatically generated and shown in cell B6. The estimated rainfall for the area of the site is automatically generated and shown in cell B7. How to fill in the table 'Wastewater load calculation table' Cell B10: Select the development type from the dropdown list. Cell B11: Enter the number of additional units being created . Cell B12: If user inputs have not been entered in the first table labelled 'Postcode lookup tool', enter the Local Planning Authority the development is within. Cell B13: Depending on the user inputs for cell B10, enter the average occupancy rate of the development. The default rate is automatically generated, this should not be edited without sufficient evidence. Cell B14: Depending on user inputs to cells B10, you will need to confirm from the dropdown list whether the default value in cell B13 has been used. Cell B15: Enter the bespoke occupancy rate, this should be supported by evidence Cell B16: Enter the per capita water usage in litres per person per day. This value should be kept at 120 unless other efficiency measures are used. Cell B17: Depending on user inputs to cell B10, enter the percentage of customers/users from outside the catchment. The default is 100 Cell B18: Depending on user inputs to cell B10, enter the number of employees per unit. Cell B19: Depending on user inputs to cell B10, enter the per capita water usage in litres per person per day for employees. This value should be kept at 120 unless other efficiency measures are used. Cell B20: Depending on the user inputs to cell B10, enter the percentage of employees from outside the catchment. Cell B21: Choose the connecting wastewater treatment works (WwTW) from the dropdown list. If you select 'Package Treatment Plant user defined' or 'Septic Tank user defined', you must enter their certified value of total phosphorus (TP) in cell B22 and their certified value of total nitrogen (TN) in cell B23. Otherwise the default values will be used in the calculation of the nutrient load associated with wastewater. | Welsh translation of filler text
|  | Table 1 subtitle | Postcode lookup tool | Welsh translation of Postcode lookup tool
|  | Table 1 heading 1 | Description of required information | Welsh translation of Description of required information
|  | Table 1 heading 2 | Data entry column- User inputs required | Welsh translation of Data entry column- User inputs required
|  | Table 2 subtitile | Wastewater load input data | Data mewnbwn llwyth dŵr gwastraff
|  | Table 2 heading 1 | Description of required information | Welsh version of Description of required information
|  | Table 2 heading 2 | Data entry column- user inputs required | Welsh version of Data entry column- user inputs required
5 | Stage 1 (Cam 1) | Heading 1 | Development proposal (number of additional units): | Cynnig datblygu (nifer o ychwanegol unedau):
5 | Stage 1 (Cam 1) | Heading (popup) 0
5 | Stage 1 (Cam 1) | Heading (popup) 1 | Default occupancy rate: | Cyfradd deiliadaeth ddiofyn:
5 | Stage 1 (Cam 1) | Heading (popup) 2 | Is this default value being used? | A yw'r gwerth rhagosodedig hwn yn cael ei ddefnyddio?
5 | Stage 1 (Cam 1) | Dropdown 1 | Yes | Oes
5 | Stage 1 (Cam 1) | Dropdown 2 | No | Nac ydw
5 | Stage 1 (Cam 1) | Heading 2 | Bespoke occupancy rate: | Cyfradd defnydd pwrpasol: | Number of customers / users per unit: | Nifer y cwsmeriaid / defnyddwyr fesul uned:
5 | Stage 1 (Cam 1) | Heading 3 | Water usage per resident (litres/person/day): | Defnydd dŵr fesul preswylydd (litr/person/diwrnod): | Water usage per customer / user (litres/person/day): | Defnydd dŵr fesul cwsmer / defnyddiwr (litr/person/diwrnod):
5 | Stage 1 (Cam 1) | Heading (popup) 3 | Percentage of customers / users from outside catchment: | Canran y cwsmeriaid / defnyddwyr o’r tu allan i’r dalgylch:
5 | Stage 1 (Cam 1) | Heading (popup) 4 | Number of employees (per unit): | Nifer y gweithwyr (fesul uned):
5 | Stage 1 (Cam 1) | Heading (popup) 5 | Water usage per employee (litres/person/day): | Defnydd dŵr fesul gweithiwr (litr/person/diwrnod):
5 | Stage 1 (Cam 1) | Heading (popup) 6 | Percentage of employees from outside catchment: | Canran y gweithwyr o’r tu allan i’r dalgylch:
5 | Stage 1 (Cam 1) | Heading 4 | Wastewater treatment works: | Gwaith trin dŵr gwastraff:
5 | Stage 1 (Cam 1) | Heading 5 | Phosphorus permitted limit (mg TP/l): | Trwydded ffosfforws a ganiateir (mg TP/l):
5 | Stage 1 (Cam 1) | Heading (popup) 7 | Phosphorus permitted limit (mg TP/l) pre 2030: | Trwydded ffosfforws (mg TP/l) cyn 2030:
5 | Stage 1 (Cam 1) | Heading 6 | Nitrogen permitted limit (mg TN/l): | Trwydded nitrogen a ganiateir (mg TN/l):
5 | Stage 1 (Cam 1) | Heading (popup) 8 | Nitrogen permitted limit (mg TN/l) pre 2030: | Trwydded nitrogen (mg TN/l) cyn 2030:
|  | Table 2 subtitle | Final calculation of nutrient load from wastewater | Cyfrifiad terfynol llwyth maetholion o ddŵr gwastraff
|  | Table 2 heading 1 | Description of values generated
|  | Table 2 heading 2 | Values generated
5 | Stage 1 (Cam 1) | Heading 7 | Additional population: | Poblogaeth ychwanegol:
5 | Stage 1 (Cam 1) | Heading 8 | Annual wastewater production (litres): | Cynhyrchu dŵr gwastraff blynyddol (litr):
5 | Stage 1 (Cam 1) | Heading 9 | Annual phosphorus load (kg TP/year): | Llwyth ffosfforws blynyddol (kg TP/blwyddyn):
5 | Stage 1 (Cam 1) | Heading 10 | Annual nitrogen load (kg TN/year): | Llwyth nitrogen blynyddol (kg TN y flwyddyn):
6 | Stage 2 (Cam 2) | Title | Stage 2 - nutrient loading from pre-existing landcovers | Cam 2 - llwytho maetholion o orchudd tir sy'n bodoli eisoes
|  | A2 Text | This sheet contains 2 tables. The tables are separated by a heading, which describes the following table. Note: You will need to fill in cells B5 to B8 in the first table labelled 'Current land use information'. Cells A6 to B8 are automatically generated and will state 'Not applicable' depending on whether user inputs are entered into the first table in stage 1 labelled 'Postcode look up table'. You will need to fill in cells A11 to B20 in the second table labelled 'Pre-existing landcovers'. Cells B21 and C11 to D21 are automatically calculated and will state '0.00' unless user inputs have been entered. Row 21 is a Totals row which automatically calculates the 'Total' sum of cells B11 to B20 in cell B21, C11 to C20 in C21 and D11 to D20 in D21. How to fill in the table 'current land use information' Cell B5: Choose the current (pre-development) soil drainage for the site being developed from the dropdown list. Cell B7: Depending on whether user inputs have been entered into table 1 in stage 1 labelled 'Postcode look up table', enter whether the automatically populated rainfall value in cell B6 is correct. Cell B8: Depending on whether user inputs have been entered into table 1 in stage 1 labelled 'Postcode look up took, select the annual average rainfall the development will receive from the dropdown list. How to fill in the table 'Pre-existing landcovers' Cell A11-B20: Choose the current existing land covers present within the redline boundary of the site pre-development. Cells B11-B20: Enter the area of each land cover in hectares The nutrient load from current land uses is automatically calculated and shown in cells C11-C20 for phosphorus (TP) and D11-D20 for nitrogen (TN). The total nutrient load from current land uses is shown in cell C21 TP and D21 for TN. | Welsh translation of Filter text on how to explain the worksheet
|  | Table 1 subtitle | Physical characteristics | Nodweddion ffisegol
|  | Table 1 heading 1 | Description of required information | Welsh version of Description on required information
|  | Table 1 heading 2 | Data entry column - user inputs required | Welsh Version of Data entry column - user inputs required
6 | Stage 2 (Cam 2) | Heading 1 | Soil drainage: | Draenio pridd:
6 | Stage 2 (Cam 2) | Dropdown 1 | Freely draining | Yn draenio'n rhydd (Freely draining)
6 | Stage 2 (Cam 2) | Dropdown 2 | Slightly impeded drainage | Rhwystro ychydig ar ddraenio (Slightly impeded drainage)
6 | Stage 2 (Cam 2) | Dropdown 3 | Impeded drainage | Rhwystro draenio (Impeded drainage)
6 | Stage 2 (Cam 2) | Dropdown 4 | Variable | Amrywiol (Variable)
6 | Stage 2 (Cam 2) | Dropdown 5 | Surface Wetness | Gwlypder Arwyneb (Surface Wetness)
6 | Stage 2 (Cam 2) | Dropdown 6 | Naturally wet | Yn naturiol wlyb (Naturally wet)
6 | Stage 2 (Cam 2) | Heading (popup) 1 | Rainfall identified using postcode (mm/year): | Glawiad wedi'i nodi gan ddefnyddio cod post (mm/blwyddyn):
6 | Stage 2 (Cam 2) | Heading (popup) 2 | Is this rainfall value correct? | A yw'r gwerth glawiad hwn yn gywir?
6 | Stage 2 (Cam 2) | Dropdown 7 | Yes | Oes
6 | Stage 2 (Cam 2) | Dropdown 8 | No | Nac ydw
6 | Stage 2 (Cam 2) | Heading (popup) 3 | Rainfall (mm/year): | Glawiad (mm/blwyddyn):
|  | Table 2 subtitle | Pre-existing landcovers | Gorchuddion tir sy'n bodoli eisoes
6 | Stage 2 (Cam 2) | Heading 2 | Landcover | Gorchudd tir
6 | Stage 2 (Cam 2) | Heading 3 | Area (hectares) | Arwynebedd (hectarau)
6 | Stage 2 (Cam 2) | Heading 4 | Phosphorus load (kg TP/year) | Llwyth ffosfforws (kg TP/blwyddyn)
6 | Stage 2 (Cam 2) | Heading 5 | Nitrogen load (kg TN/year) | Nitrogen llwyth (kg TN/blwyddyn)
|  | Heading 6 | Notes on data | Welsh transation of Notes on data
6 | Stage 2 (Cam 2) | Dropdown 9 | Cereals | Grawnfwydydd
6 | Stage 2 (Cam 2) | Dropdown 10 | General cropping | Cnydio cyffredinol
6 | Stage 2 (Cam 2) | Dropdown 11 | Horticulture | Garddwriaeth
6 | Stage 2 (Cam 2) | Dropdown 12 | Indoor pig farming | Ffermio moch dan do
6 | Stage 2 (Cam 2) | Dropdown 13 | Poultry | Dofednod
6 | Stage 2 (Cam 2) | Dropdown 14 | Dairy | Llaeth
6 | Stage 2 (Cam 2) | Dropdown 15 | Less Favoured Area grazing | Pori Ardal Lai Ffafriol
6 | Stage 2 (Cam 2) | Dropdown 16 | Lowland grazing | Pori iseldir
6 | Stage 2 (Cam 2) | Dropdown 17 | Mixed | Cymysg
6 | Stage 2 (Cam 2) | Dropdown 18 | Outdoor pig farming | Ffermio moch yn yr awyr agored
6 | Stage 2 (Cam 2) | Dropdown 19 | Greenspace | Mannau gwyrdd
6 | Stage 2 (Cam 2) | Dropdown 20 | Community food growing | Tyfu bwyd cymunedol
6 | Stage 2 (Cam 2) | Dropdown 21 | Woodland | Coetir
6 | Stage 2 (Cam 2) | Dropdown 22 | Shrub | Llwyn
6 | Stage 2 (Cam 2) | Dropdown 23 | Water | Dwfr
6 | Stage 2 (Cam 2) | Dropdown 24 | Residential land | Tir preswyl
6 | Stage 2 (Cam 2) | Dropdown 25 | Commercial/industrial land | Tir masnachol/diwydiannol
6 | Stage 2 (Cam 2) | Dropdown 26 | Open land – built environment | Tir agored – amgylchedd adeiledig
6 | Stage 2 (Cam 2) | Heading 6 | Total: | Cyfanswm:
7 | Stage 3 (Cam 3) | Title | Stage 3 - nutrient loading from new landcovers | Cam 3 - llwytho maetholion o orchudd tir newydd
|  | A2 Text | Filter text on how to explain the worksheet | Welsh translation of Filter text on how to explain the worksheet
|  | Table 1 subtitle | Total area of site | Welsh translation of Total area of site
|  | Table 2 subtitle | New landcovers | Gorchuddion tir newydd
7 | Stage 3 (Cam 3) | Heading 1 | Does Stage 2 total area match Stage 3? | Ydy cyfanswm arwynebedd Cam 2 yn cyfateb i Gam 3?
7 | Stage 3 (Cam 3) | Input 1 | Areas match | Ardaloedd sy'n cyfateb
7 | Stage 3 (Cam 3) | Input 2 | Areas do no match | Ardaloedd ddim yn cyd-fynd
7 | Stage 3 (Cam 3) | Heading (popup) 1 | Reason for mismatch: | Rheswm dros ddiffyg cyfatebiaeth:
7 | Stage 3 (Cam 3) | Input 3 | Stage 2 area larger than stage 3 | Ardal Cyfnod 2 yn fwy na chyfnod 3
7 | Stage 3 (Cam 3) | Input 4 | Stage 3 area larger than Stage 2 | Ardal Cyfnod 3 yn fwy na chyfnod 2
7 | Stage 3 (Cam 3) | Heading 2 | Landcover | Gorchudd tir
7 | Stage 3 (Cam 3) | Heading 3 | Area (hectares) | Arwynebedd (hectarau)
7 | Stage 3 (Cam 3) | Heading 4 | Phosphorus load (kg TP/ha/year) | Llwyth ffosfforws (kg TP/ha/blwyddyn)
7 | Stage 3 (Cam 3) | Heading 5 | Nitrogen load (kg TN/ha/year) | Llwyth nitrogen (kg TN/ha/blwyddyn)
7 | Stage 3 (Cam 3) | Heading 6 | Total: | Cyfanswm:
8 | Stage 3S (Cam 3S) | Heading 1 | Stage 3S - nutrient load removed through SuDS | Cam 3S - llwyth maetholion yn cael eu tynnu trwy SDCau
|  | A2 Text | This sheet contains one table. Note:You will need to fill in cells C5 to F17 if you are including SuDS to remove nutrients from the surface runoff. Cells A5 to B17 are automatically generated depending on user inputs entered in table 1 in stage 3 labelled 'New landcovers'. Cells B18, G5 to G18 and H5 to H18 are automatically calculated and will state '0.00' unless user inputs have been entered. Row 18 is a Total row. The 'Total' row automatically calculates the sum of cells B5 to B17 in cell B18, G5 to G17 in G18 and H5 to H17 in H18. How to fill in the table 'SuDS information' Cells C5-C17: Enter the size of the catchment area that drains to the SuDS feature as a proportion (%) of the landcover in the areas (in hectares) Cells D5- D17: Select the SuDS feature that is being used to treat the run off from the dropdown list. Cells E5-E17: Enter the phosphorus removal rate of the nutrient inputs as a percentage (%) Cells F5-F17: Enter the nitrogen removal rate of the nutrient inputs as a percentage (%) The annual phosphorus and nitrogen loads removed by the SuDS features are automatically calculated in cells G5 to G17 and H5-H17. These values are subtracted from the nutrient budget. The total phosphorus load removed by the SuDS feature is shown in cell G18 and the total nitrogen load removed by SuDS is shown in cell H18. | Welsh translation of Filter text on how to explain the worksheet
|  | Table 1 subtitle | SuDS information | Gwybodaeth SDCau
8 | Stage 3S (Cam 3S) | Heading 2 | Proportion of landcover area served by SuDS feature (%) | Cyfran o'r arwynebedd gorchudd tir a wasanaethir gan nodwedd SuDS (%)
8 | Stage 3S (Cam 3S) | Heading 3 | SuDS feature | Nodwedd SuDS
8 | Stage 3S (Cam 3S) | Heading 4 | P removal rate for SuDS feature | Welsh translation of P removal rate for SuDS feature
|  |  | N removal rate for SuDS feature | Welsh translation of N removal rate for SuDS feature
8 | Stage 3S (Cam 3S) | Heading 5 | Phosphorus load removed through SuDS (kg TP/year) | Ffosfforws llwyth tynnu drwy SuDS (kg TP / blwyddyn)
8 | Stage 3S (Cam 3S) | Heading 6 | Nitrogen load removed through SuDS (kg TN/year) | Nitrogen llwyth tynnu drwy SuDS (kg TN / blwyddyn)
8 | Stage 3S (Cam 3S) | Input 1 | Multi-stage management train (1+) | Trên rheoli aml-gam (1+)
8 | Stage 3S (Cam 3S) | Input 2 | Multi-stage management train (2+) | Trên rheoli aml-gam (2+)
8 | Stage 3S (Cam 3S) | Input 3 | Multi-stage management train (3+) | Trên rheoli aml-gam (3+)
8 | Stage 3S (Cam 3S) | Input 4 | Bioretention zone | Parth biogadw
8 | Stage 3S (Cam 3S) | Input 5 | Detention basin | Basn cadw
8 | Stage 3S (Cam 3S) | Input 6 | Filter drain | Draen hidlo
8 | Stage 3S (Cam 3S) | Input 7 | Filter strip | Stribed filter
8 | Stage 3S (Cam 3S) | Input 8 | Floating wetlands | Gwlyptiroedd arnofiol
8 | Stage 3S (Cam 3S) | Input 9 | Granular treatment media | Cyfryngau triniaeth gronynnog
8 | Stage 3S (Cam 3S) | Input 10 | Infiltration trenches | Ffosydd ymdreiddiad
8 | Stage 3S (Cam 3S) | Input 11 | Oil water separator | Gwahanydd dŵr olew
8 | Stage 3S (Cam 3S) | Input 12 | Permeable pavement | Palmant hydraidd
8 | Stage 3S (Cam 3S) | Input 13 | Pond | Pwll
8 | Stage 3S (Cam 3S) | Input 14 | Rainwater and stormwater storage | Storio dŵr glaw a dŵr storm
8 | Stage 3S (Cam 3S) | Input 15 | Rainwater harvesting systems | Dŵr glaw a storio stormdwr
8 | Stage 3S (Cam 3S) | Input 16 | Retention basin | Basn cadw
8 | Stage 3S (Cam 3S) | Input 17 | Soakaway / infiltration systems | Systemau ffos gerrig / ymdreiddiad
8 | Stage 3S (Cam 3S) | Input 18 | Stormwater filter | Hidlydd Stormwater
8 | Stage 3S (Cam 3S) | Input 19 | Swale | Swale
8 | Stage 3S (Cam 3S) | Input 20 | Tree pit | Pwll coed
8 | Stage 3S (Cam 3S) | Input 21 | Vortex grit separator | Gwahanydd graean vorex
8 | Stage 3S (Cam 3S) | Input 22 | Wetland | Gwlyptir
8 | Stage 3S (Cam 3S) | Input 23 | Willow beds | Gwelyau helyg
8 | Stage 4 (Cam 4) | Title | Stage 4 - final nutrient budget calculation | Cam 4 - cyfrifiad terfynol y gyllideb faetholion
|  | A2 Text | This sheet contains 2 tables. The tables are separated by a heading, which describes the following table. The tables are automatically calculated using the outputs from the previous stages. Note: You do not need to fill in any cells in the tables. Cells B5-B10 and B13-B18 are automatically calculated and will state '0.00' unless user inputs have been entered to all of the required stages. The first table labelled 'Total phosphorus nutrient budget calculation' presents the calculations that underpin the final phosphorus budget in cell B10. The second table labelled 'Total nitrogen nutrient budget calculation' presents the calculations that underpin the final phosphorus budget in cell B18. | Welsh translation of Filter text on how to explain the worksheet
|  | Table 1 subtitle | Total phosphorus budget | Cyfanswm y gyllideb ffosfforws
|  | Table 1 heading 1 | Description of phosphorus values generated | Welsh translation of description of phosphorus values generated
|  | Table 1 heading 2 | Values generated | Welsh translation of Values generated
|  | Table 2 subtitle | Total nitrogen generated | Cyfanswm y nitrogen a gynhyrchir
|  | Table 2 heading 1 | Description of nitrogen values generated | Welsh translation of description of nitrogen values generated
|  | Table 2 heading 2 | Values generated | Welsh translation of Values generated
8 | Stage 4 (Cam 4) | Heading 1 | Stage 1 phosphorus load (kg TP/year): | Llwyth ffosfforws Cam 1 (kg TP/blwyddyn):
8 | Stage 4 (Cam 4) | Heading (popup) 1 | Stage 1 phosphorus load pre 2030: | Llwyth ffosfforws Cam 1 cyn 2030:
8 | Stage 4 (Cam 4) | Heading 2 | Stage 2 phosphorus reduction (kg TP/year): | Lleihad ffosfforws Cam 2 (kg TP/blwyddyn):
8 | Stage 4 (Cam 4) | Heading 3 | Stage 3 phosphorus load (kg TP/year): | Llwyth ffosfforws Cam 3 (kg TP/blwyddyn):
8 | Stage 4 (Cam 4) | Heading 4 | Stage 3S phosphorus load removed through SuDS (kg TP/year): | Llwyth Cam 3S ffosfforws wedi'i dynnu trwy SuDS (kg TP / blwyddyn):
8 | Stage 4 (Cam 4) | Heading 5 | Phosphorus budget ((Stage 1 - Stage 2) + (Stage 3 - Stage 3S)): | Cyllideb ffosfforws ((Cam 1 - Cam 2) + (Cam 3 - Cam 3S)):
8 | Stage 4 (Cam 4) | Heading 6 | Phosphorus budget + 20% buffer | Cyllideb ffosfforws + byffer 20%.
8 | Stage 4 (Cam 4) | Heading (popup) 2 | Phosphorus budget for first x years: | P cyllideb ar gyfer x blwyddyn gyntaf:
8 | Stage 4 (Cam 4) | Heading 7 | Stage 1 nitrogen load (kg TN/year): | Llwyth nitrogen Cam 1 (kg TN/blwyddyn):
8 | Stage 4 (Cam 4) | Heading (popup) 3 | Stage 1 nitrogen load pre 2030: | Llwyth nitrogen Cam 1 cyn 2030:
8 | Stage 4 (Cam 4) | Heading 8 | Stage 2 nitrogen reduction (kg TN/year): | Lleihad nitrogen Cam 2 (kg TN/blwyddyn):
8 | Stage 4 (Cam 4) | Heading 9 | Stage 3 nitrogen load (kg TN/year): | Llwyth nitrogen Cam 3 (kg TN/blwyddyn):
8 | Stage 4 (Cam 4) | Heading 10 | Stage 3S nitrogen load removed through SuDS (TN kg/year): | Llwyth Cam 3S nitrogen wedi'i dynnu trwy SuDS (kg TN /blwyddyn):
8 | Stage 4 (Cam 4) | Heading 11 | Nitrogen budget ((Stage 1 - Stage 2) + (Stage 3 - Stage 3S)): | Nitrogen cyllideb ((Cam 1 - Cam 2) + (Cam 3 - Cam 3S)):
8 | Stage 4 (Cam 4) | Heading 12 | Nitrogen budget + 20% buffer: | Nitrogen cyllideb + byffer 20%:
8 | Stage 4 (Cam 4) | Heading (popup) 4 | Nitrogen budget for first x years: | Nitrogen cyllideb am x blwyddyn gyntaf:
9 | Descriptions (Disgrifiadau) | Title | Input descriptions | Disgrifiadau mewnbwn
9 | Descriptions (Disgrifiadau) | Subtitle | Landcover descriptions | Disgrifiadau gorchudd tir
9 | Descriptions (Disgrifiadau) | Heading 1 | Cereals | Grawnfwydydd
9 | Descriptions (Disgrifiadau) | Heading 2 | General | Cyffredinol
9 | Descriptions (Disgrifiadau) | Heading 3 | Horticulture | Garddwriaeth
9 | Descriptions (Disgrifiadau) | Heading 4 | Indoor Pig farming | Ffermio moch dan do
9 | Descriptions (Disgrifiadau) | Heading 5 | Outdoor Pig farming | Ffermio moch yn yr awyr agored
9 | Descriptions (Disgrifiadau) | Heading 6 | Poultry | Dofednod
9 | Descriptions (Disgrifiadau) | Heading 7 | Dairy | Llaeth
9 | Descriptions (Disgrifiadau) | Heading 8 | Less Favoured Area (LFA) grazing | Pori Ardal Lai Ffafriol (LFA)
9 | Descriptions (Disgrifiadau) | Heading 9 | Lowland grazing | Pori iseldir
9 | Descriptions (Disgrifiadau) | Heading 10 | Mixed | Cymysg
9 | Descriptions (Disgrifiadau) | Heading 11 | Greenspace | Mannau gwyrdd
9 | Descriptions (Disgrifiadau) | Heading 12 | Woodland | Coetir
9 | Descriptions (Disgrifiadau) | Heading 13 | Shrub | Llwyn
9 | Descriptions (Disgrifiadau) | Heading 14 | Water | Dwfr
9 | Descriptions (Disgrifiadau) | Heading 15 | Residential land | Tir preswyl
9 | Descriptions (Disgrifiadau) | Heading 16 | Commercial / industrial land | Tir masnachol / diwydiannol
9 | Descriptions (Disgrifiadau) | Heading 17 | Open land – built environment | Tir agored – amgylchedd adeiledig
9 | Descriptions (Disgrifiadau) | Heading 18 | Community food growing | Tyfu bwyd cymunedol
9 | Descriptions (Disgrifiadau) | Description 1 | Agricultural areas on which cereals, combinable crops and set aside are farmed. | Ardaloedd amaethyddol lle mae grawnfwydydd, cnydau cyfunadwy a neilltir yn cael eu ffermio.
9 | Descriptions (Disgrifiadau) | Description 2 | Agricultural areas on which arable crops (including field scale vegetables) are farmed. | Ardaloedd amaethyddol lle mae cnydau âr (gan gynnwys llysiau caeau) yn cael eu ffermio.
9 | Descriptions (Disgrifiadau) | Description 3 | Agricultural areas on which fruit (including vineyards), hardy nursery stock, glasshouse flowers and vegetables, market garden scale vegetables, outdoor bulbs and flowers, and mushrooms are farmed. | Ardaloedd amaethyddol lle mae ffrwythau (gan gynnwys gwinllannoedd), stoc meithrinfa wydn, blodau a llysiau tŷ gwydr, llysiau graddfa gardd farchnad, bylbiau a blodau awyr agored, a madarch yn cael eu ffermio.
9 | Descriptions (Disgrifiadau) | Description 4 | Agricultural areas on which pigs farmed indoors. | Ardaloedd amaethyddol lle'r oedd moch yn ffermio dan do.
9 | Descriptions (Disgrifiadau) | Description 5 | Agricultural areas on which pigs farmed outdoors. | Ardaloedd amaethyddol lle roedd moch yn ffermio yn yr awyr agored.
9 | Descriptions (Disgrifiadau) | Description 6 | Agricultural areas on which poultry are farmed. | Ardaloedd amaethyddol lle mae dofednod yn cael eu ffermio.
9 | Descriptions (Disgrifiadau) | Description 7 | Agricultural areas on which dairy cows are farmed. | Ardaloedd amaethyddol lle mae gwartheg godro yn cael eu ffermio.
9 | Descriptions (Disgrifiadau) | Description 8 | Agricultural areas on which cattle, sheep and other grazing livestock are farmed in locations where agricultural production is difficult. An area is classified as an LFA holding if 50 per cent or more of its total area is classed as LFA. | Ardaloedd amaethyddol lle mae gwartheg, defaid a da byw pori eraill yn cael eu ffermio mewn lleoliadau lle mae cynhyrchu amaethyddol yn anodd. Mae ardal yn cael ei dosbarthu fel daliad ALFf os yw 50 y cant neu fwy o'i holl arwynebedd yn cael ei ddosbarthu fel ALFf.
9 | Descriptions (Disgrifiadau) | Description 9 | Agricultural areas on which cattle, sheep and other grazing livestock are farmed. A holding is classified as lowland if less than 50 per cent of its total area is classed as a lowland grazing area. | Ardaloedd amaethyddol lle mae gwartheg, defaid a da byw pori eraill yn cael eu ffermio. Dosberthir daliad fel tir isel os yw llai na 50 y cant o gyfanswm ei arwynebedd yn cael ei ddosbarthu fel ardal bori iseldir.
9 | Descriptions (Disgrifiadau) | Description 10 | Agricultural areas in which none of the above categories are farmed or where it is too difficult to select a single category to describe the farm type. This farm type does not include horticultural crops or outdoor pig farming. | Ardaloedd amaethyddol lle nad oes yr un o’r categorïau uchod yn cael ei ffermio neu lle mae’n rhy anodd dewis un categori i ddisgrifio’r math o fferm. Nid yw'r math hwn o fferm yn cynnwys cnydau garddwriaethol na ffermio moch yn yr awyr agored.
9 | Descriptions (Disgrifiadau) | Description 11 | Natural and semi-natural outdoor spaces provided for recreational use where fertilisers will not be applied and dog waste is managed, e.g. semi-natural parks. This does not include green infrastructure within the built urban environment, such as gardens, or grass verges, as these are included in the residential urban land category for residential developments, or the open land – built environment category for all other development types. | Mannau awyr agored naturiol a lled-naturiol a ddarperir ar gyfer defnydd hamdden lle na fydd gwrtaith yn cael ei wasgaru a lle mae gwastraff cŵn yn cael ei reoli, e.e. parciau lled-naturiol. Nid yw hyn yn cynnwys seilwaith gwyrdd o fewn yr amgylchedd trefol adeiledig, megis gerddi, neu ymylon glaswelltog, gan fod y rhain wedi’u cynnwys yn y categori tir trefol preswyl ar gyfer datblygiadau preswyl, neu’r categori tir agored – amgylchedd adeiledig ar gyfer pob math arall o ddatblygiad.
9 | Descriptions (Disgrifiadau) | Description 12 | Natural and semi-natural outdoor wooded areas. | Ardaloedd coediog awyr agored naturiol a lled-naturiol.
9 | Descriptions (Disgrifiadau) | Description 13 | Natural and semi-natural outdoor shrubland area. | Ardal llwyni awyr agored naturiol a lled-naturiol.
9 | Descriptions (Disgrifiadau) | Description 14 | Areas of surface water that remain inundated all year round, including rivers, ponds, and lakes. | Ardaloedd o ddŵr wyneb sy’n parhau i fod dan ddŵr drwy gydol y flwyddyn, gan gynnwys afonydd, pyllau a llynnoedd.
9 | Descriptions (Disgrifiadau) | Description 15 | Areas of houses and associated infrastructure. This is inclusive of residential roads, driveways, grass verges, gardens and SuDS infrastructure that drains a residential development | Ardaloedd o dai a seilwaith cysylltiedig. Mae hyn yn cynnwys ffyrdd preswyl, tramwyfeydd, ymylon glaswelltog, gerddi a seilwaith SuDS sy'n draenio datblygiad preswyl
9 | Descriptions (Disgrifiadau) | Description 16 | Areas that are used for industry. These are businesses that typically manufacture, process or otherwise generate products. Included in the definition of industrial land are factories and storage facilities as well as mining and shipping operations. | Ardaloedd a ddefnyddir ar gyfer diwydiant. Mae'r rhain yn fusnesau sydd fel arfer yn gweithgynhyrchu, prosesu neu gynhyrchu cynhyrchion fel arall. Yn gynwysedig yn y diffiniad o dir diwydiannol mae ffatrïoedd a chyfleusterau storio yn ogystal â gweithrediadau mwyngloddio a llongau.
9 | Descriptions (Disgrifiadau) | Description 17 | Areas of land in urban areas used for various purposes, e.g. main roads, built facilities such as schools, sports centres, areas used for leisure and recreation - this may include open land, e.g. caravan sites, camping sites, sports fields, playgrounds, public squares and SuDS in a non-residential context. | Ardaloedd o dir mewn ardaloedd trefol a ddefnyddir at wahanol ddibenion, e.e. prif ffyrdd, cyfleusterau adeiledig fel ysgolion, canolfannau chwaraeon, ardaloedd a ddefnyddir ar gyfer hamdden ac adloniant - gall hyn gynnwys tir agored, e.e. safleoedd carafanau, meysydd gwersylla, meysydd chwarae, meysydd chwarae, sgwariau cyhoeddus a SuDS mewn cyd-destun dibreswyl.
9 | Descriptions (Disgrifiadau) | Description 18 | Areas that are used for local food production, such as allotments. | Ardaloedd a ddefnyddir ar gyfer cynhyrchu bwyd lleol, megis rhandiroedd.
9 | Descriptions (Disgrifiadau) | Subtitle | Development types and planning permission use classes | Mathau o ddatblygiad a dosbarthiadau defnydd caniatâd cynllunio
9 | Descriptions (Disgrifiadau) | Heading 19 | Residential | Preswyl
9 | Descriptions (Disgrifiadau) | Heading 20 | Commercial | Masnachol
9 | Descriptions (Disgrifiadau) | Heading 21 | Leisure | Hamdden
9 | Descriptions (Disgrifiadau) | Heading 22 | Public service infrastructure | Seilwaith gwasanaethau cyhoeddus
9 | Descriptions (Disgrifiadau) | Heading 23 | Tourism | Twristiaeth
9 | Descriptions (Disgrifiadau) | Description 19 | C2 Residential institutions; C2A Secure Residential Institution; C3 Dwellinghouses, used as sole or main residences; C4 Houses in multiple occupation; C5 Dwellinghouses, used otherwise than as sole or main residences; C6 Short term | C2 Sefydliadau preswyl; Sefydliad Preswyl Diogel C2A; C3 Anheddau, a ddefnyddir fel unig neu brif breswylfeydd; C4 Tai amlfeddiannaeth; C5 Anheddau, a ddefnyddir heblaw fel unig neu brif breswylfeydd; C6 Tymor byr
9 | Descriptions (Disgrifiadau) | Description 20 | A1 Shops; A2 Financial and professional services; A3 Food and drink; B1 Business; B2 General industrial; B8 Storage or distribution | Siopau A1; A2 Gwasanaethau ariannol a phroffesiynol; A3 Bwyd a diod; B1 Busnes; B2 Diwydiannol cyffredinol; B8 Storio neu ddosbarthu
9 | Descriptions (Disgrifiadau) | Description 21 | D2 Assembly and leisure | D2 Ymgynnull a hamdden
9 | Descriptions (Disgrifiadau) | Description 22 | D1 Non-residential institutions | D1 Sefydliadau dibreswyl
9 | Descriptions (Disgrifiadau) | Description 23 | C1 Hotels | C1 Gwestai
|  | Package treatment plant (PTP) default |  | Offer trin pecyn (PTP) rhagosodedig
|  | Package treatment plant (PTP) user defined | Enter the bespoke P permit (mg TP/l): | Rhowch y drwydded P pwrpasol (mg TP/l): | Enter the bespoke N permit (mg TN/l): | Rhowch y drwydded N pwrpasol (mg TN/l):
|  | Septic tank default |  | Tanc septig rhagosodedig
|  | Septic tank user defined |  | Defnyddiwr tanc septig wedi'i ddiffinio
|  |  | Lookup tables | Tablau edrych

## Postcode_Lookup (hidden)
postcode | postcode_nospace | postcode_lc | Postcode_lc_ns | LPA | LPA_C | HubName | Nearest_WwTW | SAAR_Round | Farmscoper_Equivalent | Residential P export coefficient (kg/ha/yr) | Commercial / industrial P export coefficient (kg/ha/yr) | Open urban P export coefficient (kg/ha/yr) | Residential N export coefficient (kg/ha/yr) | Commercial / industrial N export coefficient (kg/ha/yr) | Open urban N export coefficient (kg/ha/yr) | X | Y | Previous_LPA_Name | Agricultural_Region | SAC_Name | Welsh LPA Name | English LPA name
LL40 2DU | LL402DU | ll40 2du | ll402du | Gwynedd | Gwynedd | Llanfachreth WwTW | 695 | 1804 | Over1500 | 3.61 | 2.64 | 1.94 | 33.62 | 17.93 | 19.82 | 276058 | 322224 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Blaenau Gwent LPA | Blaenau Gwent LPA | Blaenau Gwent County Borough Council | Cyngor Bwrdeistref Sirol Blaenau Gwent
LL40 2DY | LL402DY | ll40 2dy | ll402dy | Gwynedd | Gwynedd | Llanfachreth WwTW | 236 | 1728 | Over1500 | 3.46 | 2.53 | 1.86 | 32.21 | 17.18 | 18.99 | 275520 | 322527 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Brecon Beacons National Park LPA |  | Bridgend County Borough Council | Cyngor Bwrdeistref Sirol Pen-y-bont ar Ogwr
LL40 2EA | LL402EA | ll40 2ea | ll402ea | Gwynedd | Gwynedd | Llanfachreth WwTW | 137 | 1729 | Over1500 | 3.46 | 2.53 | 1.86 | 32.23 | 17.19 | 19 | 275466 | 322444 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Carmarthenshire LPA |  | Caerphilly County Borough Council | Cyngor Bwrdeistref Sirol Caerffili
LL40 2EB | LL402EB | ll40 2eb | ll402eb | Gwynedd | Gwynedd | Llanfachreth WwTW | 257 | 1729 | Over1500 | 3.46 | 2.53 | 1.86 | 32.23 | 17.19 | 19 | 275148 | 322468 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Ceredigion LPA |  | Cardiff Council | Cyngor Caerdydd
LL40 2ED | LL402ED | ll40 2ed | ll402ed | Gwynedd | Gwynedd | Llanfachreth WwTW | 161 | 1780 | Over1500 | 3.56 | 2.61 | 1.91 | 33.18 | 17.69 | 19.56 | 275354 | 322503 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Conwy LPA | Carmarthenshire LPA | Carmarthenshire County Council | Cyngor Sir Gaerfyrddin
LL40 2EE | LL402EE | ll40 2ee | ll402ee | Gwynedd | Gwynedd | Llanfachreth WwTW | 206 | 1780 | Over1500 | 3.56 | 2.61 | 1.91 | 33.18 | 17.69 | 19.56 | 275443 | 322537 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Denbighshire LPA | Ceredigion LPA | Ceredigion County Council | Cyngor Sir Ceredigion
LL40 2EF | LL402EF | ll40 2ef | ll402ef | Gwynedd | Gwynedd | Llanfachreth WwTW | 211 | 1780 | Over1500 | 3.56 | 2.61 | 1.91 | 33.18 | 17.69 | 19.56 | 275467 | 322532 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Flintshire LPA | Conwy LPA | Conwy County Borough Council | Cyngor Bwrdeistref Sirol Conwy
LL40 2EG | LL402EG | ll40 2eg | ll402eg | Gwynedd | Gwynedd | Llanfachreth WwTW | 837 | 1728 | Over1500 | 3.46 | 2.53 | 1.86 | 32.21 | 17.18 | 18.99 | 275525 | 323166 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Gwynedd LPA | Denbighshire LPA | Denbighshire County Council | Cyngor Sir Ddinbych
LL40 2EH | LL402EH | ll40 2eh | ll402eh | Gwynedd | Gwynedd | Llanfachreth WwTW | 1032 | 1728 | Over1500 | 3.46 | 2.53 | 1.86 | 32.21 | 17.18 | 18.99 | 276363 | 322632 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Monmouthshire LPA | Flintshire LPA | Flintshire County Council | Cyngor Sir y Fflint
LL40 2HB | LL402HB | ll40 2hb | ll402hb | Gwynedd | Gwynedd | Llanfachreth WwTW | 4372 | 1675 | Over1500 | 3.35 | 2.45 | 1.8 | 31.22 | 16.65 | 18.4 | 272288 | 319246 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Neath Port Talbot LPA | Gwynedd LPA | Gwynedd Council | Cyngor Gwynedd
LL40 2HD | LL402HD | ll40 2hd | ll402hd | Gwynedd | Gwynedd | Llanfachreth WwTW | 3698 | 1711 | Over1500 | 3.42 | 2.51 | 1.84 | 31.89 | 17.01 | 18.8 | 272356 | 320206 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Newport LPA |  | Isle of Anglesey County Council | Cyngor Sir Ynys Môn
LL40 2HE | LL402HE | ll40 2he | ll402he | Gwynedd | Gwynedd | Llanfachreth WwTW | 4314 | 1711 | Over1500 | 3.42 | 2.51 | 1.84 | 31.89 | 17.01 | 18.8 | 272087 | 319549 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Pembrokeshire Coast National Park LPA |  | Merthyr Tydfil County Borough Council | Cyngor Bwrdeistref Sirol Merthyr Tudful
LL40 2HF | LL402HF | ll40 2hf | ll402hf | Gwynedd | Gwynedd | Ganllwyd STW | 3080 | 1694 | Over1500 | 3.39 | 2.48 | 1.82 | 31.57 | 16.84 | 18.61 | 272491 | 321046 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Pembrokeshire LPA | Monmouthshire LPA | Monmouthshire County Council | Cyngor Sir Fynwy
LL40 2HG | LL402HG | ll40 2hg | ll402hg | Gwynedd | Gwynedd | Llanfachreth WwTW | 2182 | 1931 | Over1500 | 3.86 | 2.83 | 2.07 | 35.99 | 19.2 | 21.22 | 273235 | 321909 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Powys LPA | Neath Port Talbot LPA | Neath Port Talbot County Borough Council | Cyngor Bwrdeistref Sirol Castell-nedd Port Talbot
LL40 2HH | LL402HH | ll40 2hh | ll402hh | Gwynedd | Gwynedd | Ganllwyd STW | 1910 | 1931 | Over1500 | 3.86 | 2.83 | 2.07 | 35.99 | 19.2 | 21.22 | 273350 | 322281 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Snowdonia National Park LPA | Newport LPA | Newport City Council | Cyngor Dinas Casnewydd
LL40 2HL | LL402HL | ll40 2hl | ll402hl | Gwynedd | Gwynedd | Ganllwyd STW | 1278 | 1956 | Over1500 | 3.92 | 2.86 | 2.1 | 36.46 | 19.44 | 21.49 | 272917 | 322838 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Swansea LPA | Pembrokeshire LPA | Pembrokeshire County Council | Cyngor Sir Penfro
LL40 2HN | LL402HN | ll40 2hn | ll402hn | Gwynedd | Gwynedd | Ganllwyd STW | 840 | 1956 | Over1500 | 3.92 | 2.86 | 2.1 | 36.46 | 19.44 | 21.49 | 272744 | 323272 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Torfaen LPA | Powys LPA | Powys County Council | Cyngor Sir Powys
LL40 2HP | LL402HP | ll40 2hp | ll402hp | Gwynedd | Gwynedd | Ganllwyd STW | 247 | 1900 | Over1500 | 3.8 | 2.78 | 2.04 | 35.41 | 18.89 | 20.88 | 272576 | 324005 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park | Wrexham LPA |  | Rhondda Cynon Taf County Borough Council | Cyngor Bwrdeistref Sirol Rhondda Cynon Taf
LL40 2HR | LL402HR | ll40 2hr | ll402hr | Gwynedd | Gwynedd | Ganllwyd STW | 570 | 1829 | Over1500 | 3.66 | 2.68 | 1.96 | 34.09 | 18.18 | 20.09 | 272695 | 324670 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park |  | Swansea LPA | Swansea Council | Cyngor a Dinas Abertawe
LL40 2HS | LL402HS | ll40 2hs | ll402hs | Gwynedd | Gwynedd | Ganllwyd STW | 2620 | 1902 | Over1500 | 3.81 | 2.79 | 2.04 | 35.45 | 18.91 | 20.9 | 273498 | 326635 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park |  | Torfaen LPA | Torfaen County Borough Council | Cyngor Bwrdeistref Sirol Torfaen
LL40 2HT | LL402HT | ll40 2ht | ll402ht | Gwynedd | Gwynedd | Ganllwyd STW | 798 | 1829 | Over1500 | 3.66 | 2.68 | 1.96 | 34.09 | 18.18 | 20.09 | 272732 | 324905 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park |  |  | Vale of Glamorgan Council | Cyngor Bro Morgannwg
LL40 2HU | LL402HU | ll40 2hu | ll402hu | Gwynedd | Gwynedd | Ganllwyd STW | 1200 | 1829 | Over1500 | 3.66 | 2.68 | 1.96 | 34.09 | 18.18 | 20.09 | 272557 | 325285 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park |  | Wrexham LPA | Wrexham County Borough Council | Cyngor Bwrdeistref Sirol Wrecsam
LL40 2HW | LL402HW | ll40 2hw | ll402hw | Gwynedd | Gwynedd | Ganllwyd STW | 586 | 1959 | Over1500 | 3.92 | 2.87 | 2.1 | 36.51 | 19.47 | 21.52 | 272496 | 323609 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park |  | Brecon Beacons National Park LPA | Bannau Brycheiniog National Park | Parc Cenedlaethol Bannau Brycheiniog
LL40 2HY | LL402HY | ll40 2hy | ll402hy | Gwynedd | Gwynedd | Ganllwyd STW | 3739 | 1988 | Over1500 | 3.98 | 2.91 | 2.14 | 37.05 | 19.76 | 21.84 | 271594 | 327648 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park |  | Pembrokeshire Coast National Park LPA | Pembrokeshire Coast National Park | Parc Cenedlaethol Arfordir Penfro
LL40 2HZ | LL402HZ | ll40 2hz | ll402hz | Gwynedd | Gwynedd | Ganllwyd STW | 3192 | 2018 | Over1500 | 4.04 | 2.96 | 2.17 | 37.61 | 20.06 | 22.17 | 271906 | 327174 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park |  | Snowdonia National Park LPA | Eryri National Park | Parc Cenedlaethol Eryri
LL40 2LA | LL402LA | ll40 2la | ll402la | Gwynedd | Gwynedd | Bronaber STW | 3541 | 2070 | Over1500 | 4.14 | 3.03 | 2.22 | 38.58 | 20.58 | 22.74 | 271050 | 327910 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2LB | LL402LB | ll40 2lb | ll402lb | Gwynedd | Gwynedd | Bronaber STW | 2773 | 2215 | Over1500 | 4.43 | 3.24 | 2.38 | 41.28 | 22.02 | 24.34 | 270481 | 328619 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2LD | LL402LD | ll40 2ld | ll402ld | Gwynedd | Gwynedd | Bronaber STW | 3673 | 1988 | Over1500 | 3.98 | 2.91 | 2.14 | 37.05 | 19.76 | 21.84 | 272178 | 328177 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2LE | LL402LE | ll40 2le | ll402le | Gwynedd | Gwynedd | Ganllwyd STW | 1968 | 1931 | Over1500 | 3.86 | 2.83 | 2.07 | 35.99 | 19.2 | 21.22 | 273006 | 326067 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2LF | LL402LF | ll40 2lf | ll402lf | Gwynedd | Gwynedd | Ganllwyd STW | 3435 | 1898 | Over1500 | 3.8 | 2.78 | 2.04 | 35.38 | 18.87 | 20.85 | 274107 | 327286 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2LG | LL402LG | ll40 2lg | ll402lg | Gwynedd | Gwynedd | Ganllwyd STW | 1331 | 1869 | Over1500 | 3.74 | 2.74 | 2.01 | 34.84 | 18.58 | 20.53 | 273795 | 324994 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2LH | LL402LH | ll40 2lh | ll402lh | Gwynedd | Gwynedd | Ganllwyd STW | 2179 | 1991 | Over1500 | 3.99 | 2.92 | 2.14 | 37.11 | 19.79 | 21.87 | 274200 | 325779 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2LL | LL402LL | ll40 2ll | ll402ll | Gwynedd | Gwynedd | Ganllwyd STW | 1203 | 1802 | Over1500 | 3.61 | 2.64 | 1.94 | 33.59 | 17.91 | 19.8 | 273993 | 324263 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2LW | LL402LW | ll40 2lw | ll402lw | Gwynedd | Gwynedd | Ganllwyd STW | 4744 | 1916 | Over1500 | 3.83 | 2.81 | 2.06 | 35.71 | 19.05 | 21.05 | 275269 | 328160 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2NH | LL402NH | ll40 2nh | ll402nh | Gwynedd | Gwynedd | Llanfachreth WwTW | 351 | 1729 | Over1500 | 3.46 | 2.53 | 1.86 | 32.23 | 17.19 | 19 | 275069 | 322168 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2NL | LL402NL | ll40 2nl | ll402nl | Gwynedd | Gwynedd | Llanfachreth WwTW | 801 | 1729 | Over1500 | 3.46 | 2.53 | 1.86 | 32.23 | 17.19 | 19 | 274618 | 322077 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2NN | LL402NN | ll40 2nn | ll402nn | Gwynedd | Gwynedd | Llanfachreth WwTW | 1046 | 1767 | Over1500 | 3.54 | 2.59 | 1.9 | 32.93 | 17.56 | 19.41 | 274328 | 322371 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2NP | LL402NP | ll40 2np | ll402np | Gwynedd | Gwynedd | Llanfachreth WwTW | 2538 | 1782 | Over1500 | 3.57 | 2.61 | 1.91 | 33.21 | 17.71 | 19.58 | 273037 | 321352 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2NR | LL402NR | ll40 2nr | ll402nr | Gwynedd | Gwynedd | Llanfachreth WwTW | 833 | 1780 | Over1500 | 3.56 | 2.61 | 1.91 | 33.18 | 17.69 | 19.56 | 274581 | 322602 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2NS | LL402NS | ll40 2ns | ll402ns | Gwynedd | Gwynedd | Llanfachreth WwTW | 1107 | 1780 | Over1500 | 3.56 | 2.61 | 1.91 | 33.18 | 17.69 | 19.56 | 274738 | 323249 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2NT | LL402NT | ll40 2nt | ll402nt | Gwynedd | Gwynedd | Llanfachreth WwTW | 1479 | 1828 | Over1500 | 3.66 | 2.68 | 1.96 | 34.07 | 18.17 | 20.08 | 274025 | 322952 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2NU | LL402NU | ll40 2nu | ll402nu | Gwynedd | Gwynedd | Llanfachreth WwTW | 818 | 1780 | Over1500 | 3.56 | 2.61 | 1.91 | 33.18 | 17.69 | 19.56 | 274652 | 322730 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2NW | LL402NW | ll40 2nw | ll402nw | Gwynedd | Gwynedd | Ganllwyd STW | 1631 | 1828 | Over1500 | 3.66 | 2.68 | 1.96 | 34.07 | 18.17 | 20.08 | 273511 | 322643 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2NY | LL402NY | ll40 2ny | ll402ny | Gwynedd | Gwynedd | Ganllwyd STW | 2618 | 1886 | Over1500 | 3.77 | 2.76 | 2.03 | 35.15 | 18.75 | 20.72 | 275152 | 325259 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2PA | LL402PA | ll40 2pa | ll402pa | Gwynedd | Gwynedd | Ganllwyd STW | 2545 | 2043 | Over1500 | 4.09 | 2.99 | 2.19 | 38.08 | 20.31 | 22.45 | 274878 | 325578 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2PB | LL402PB | ll40 2pb | ll402pb | Gwynedd | Gwynedd | Ganllwyd STW | 2208 | 1886 | Over1500 | 3.77 | 2.76 | 2.03 | 35.15 | 18.75 | 20.72 | 274534 | 325477 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2PD | LL402PD | ll40 2pd | ll402pd | Gwynedd | Gwynedd | Ganllwyd STW | 2496 | 2043 | Over1500 | 4.09 | 2.99 | 2.19 | 38.08 | 20.31 | 22.45 | 274525 | 325913 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2PE | LL402PE | ll40 2pe | ll402pe | Gwynedd | Gwynedd | Ganllwyd STW | 2805 | 2043 | Over1500 | 4.09 | 2.99 | 2.19 | 38.08 | 20.31 | 22.45 | 275043 | 325794 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2PF | LL402PF | ll40 2pf | ll402pf | Gwynedd | Gwynedd | Ganllwyd STW | 5404 | 2062 | Over1500 | 4.13 | 3.02 | 2.21 | 38.43 | 20.5 | 22.65 | 276668 | 327882 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2PG | LL402PG | ll40 2pg | ll402pg | Gwynedd | Gwynedd | Bronaber STW | 5803 | 1962 | Over1500 | 3.93 | 2.87 | 2.11 | 36.57 | 19.5 | 21.56 | 275828 | 329341 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2PH | LL402PH | ll40 2ph | ll402ph | Gwynedd | Gwynedd | Ganllwyd STW | 4177 | 1987 | Over1500 | 3.98 | 2.91 | 2.13 | 37.03 | 19.75 | 21.83 | 273454 | 328235 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2ST | LL402ST | ll40 2st | ll402st | Gwynedd | Gwynedd | Llanfachreth WwTW | 4533 | 1711 | Over1500 | 3.42 | 2.51 | 1.84 | 31.89 | 17.01 | 18.8 | 271794 | 319562 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2SU | LL402SU | ll40 2su | ll402su | Gwynedd | Gwynedd | Llanfachreth WwTW | 4472 | 1711 | Over1500 | 3.42 | 2.51 | 1.84 | 31.89 | 17.01 | 18.8 | 271738 | 319739 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2SY | LL402SY | ll40 2sy | ll402sy | Gwynedd | Gwynedd | Llanfachreth WwTW | 4250 | 1711 | Over1500 | 3.42 | 2.51 | 1.84 | 31.89 | 17.01 | 18.8 | 271905 | 319887 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2TF | LL402TF | ll40 2tf | ll402tf | Gwynedd | Gwynedd | Ganllwyd STW | 353 | 1900 | Over1500 | 3.8 | 2.78 | 2.04 | 35.41 | 18.89 | 20.88 | 272702 | 324449 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2TG | LL402TG | ll40 2tg | ll402tg | Gwynedd | Gwynedd | Ganllwyd STW | 501 | 1829 | Over1500 | 3.66 | 2.68 | 1.96 | 34.09 | 18.18 | 20.09 | 272699 | 324601 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2TH | LL402TH | ll40 2th | ll402th | Gwynedd | Gwynedd | Ganllwyd STW | 477 | 1829 | Over1500 | 3.66 | 2.68 | 1.96 | 34.09 | 18.18 | 20.09 | 272676 | 324571 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2TL | LL402TL | ll40 2tl | ll402tl | Gwynedd | Gwynedd | Ganllwyd STW | 190 | 1900 | Over1500 | 3.8 | 2.78 | 2.04 | 35.41 | 18.89 | 20.88 | 272816 | 324299 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2TN | LL402TN | ll40 2tn | ll402tn | Gwynedd | Gwynedd | Ganllwyd STW | 937 | 1959 | Over1500 | 3.92 | 2.87 | 2.1 | 36.51 | 19.47 | 21.52 | 271864 | 324140 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2TP | LL402TP | ll40 2tp | ll402tp | Gwynedd | Gwynedd | Ganllwyd STW | 2223 | 1931 | Over1500 | 3.86 | 2.83 | 2.07 | 35.99 | 19.2 | 21.22 | 272730 | 321889 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2TW | LL402TW | ll40 2tw | ll402tw | Gwynedd | Gwynedd | Ganllwyd STW | 1316 | 1956 | Over1500 | 3.92 | 2.86 | 2.1 | 36.46 | 19.44 | 21.49 | 272507 | 322827 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL40 2UT | LL402UT | ll40 2ut | ll402ut | Gwynedd | Gwynedd | Llanfachreth WwTW | 113 | 1729 | Over1500 | 3.46 | 2.53 | 1.86 | 32.23 | 17.19 | 19 | 275320 | 322443 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL41 4UP | LL414UP | ll41 4up | ll414up | Gwynedd | Gwynedd | Bronaber STW | 2031 | 1953 | Over1500 | 3.91 | 2.86 | 2.1 | 36.4 | 19.41 | 21.46 | 270871 | 333365 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL41 4UR | LL414UR | ll41 4ur | ll414ur | Gwynedd | Gwynedd | Bronaber STW | 969 | 2018 | Over1500 | 4.04 | 2.96 | 2.17 | 37.61 | 20.06 | 22.17 | 271248 | 331859 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL41 4UT | LL414UT | ll41 4ut | ll414ut | Gwynedd | Gwynedd | Bronaber STW | 916 | 2018 | Over1500 | 4.04 | 2.96 | 2.17 | 37.61 | 20.06 | 22.17 | 270678 | 332263 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL41 4UY | LL414UY | ll41 4uy | ll414uy | Gwynedd | Gwynedd | Bronaber STW | 2208 | 2055 | Over1500 | 4.11 | 3.01 | 2.21 | 38.3 | 20.43 | 22.58 | 272527 | 331981 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL41 4YB | LL414YB | ll41 4yb | ll414yb | Gwynedd | Gwynedd | Bronaber STW | 1315 | 2067 | Over1500 | 4.14 | 3.03 | 2.22 | 38.53 | 20.55 | 22.71 | 271597 | 331933 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL41 4YD | LL414YD | ll41 4yd | ll414yd | Gwynedd | Gwynedd | Bronaber STW | 2401 | 2062 | Over1500 | 4.13 | 3.02 | 2.21 | 38.43 | 20.5 | 22.65 | 271473 | 329243 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL41 4YE | LL414YE | ll41 4ye | ll414ye | Gwynedd | Gwynedd | Bronaber STW | 1888 | 2050 | Over1500 | 4.1 | 3 | 2.2 | 38.21 | 20.38 | 22.52 | 270730 | 329531 | Snowdonia National Park LPA | NW | Afon Eden - Cors Goch Trawsfynydd | Parc Cenedlaethol Eryri | Eryri National Park
LL54 5RB | LL545RB | ll54 5rb | ll545rb | Gwynedd | Gwynedd | Llanfaglan WwTW | 33 | 1112 | 900to1200 | 2.23 | 1.63 | 1.19 | 20.73 | 11.05 | 12.22 | 246648 | 359345 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 5TY | LL545TY | ll54 5ty | ll545ty | Gwynedd | Gwynedd | Llanfaglan WwTW | 1151 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 247632 | 359928 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 5UL | LL545UL | ll54 5ul | ll545ul | Gwynedd | Gwynedd | Llanfaglan WwTW | 1180 | 996 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.56 | 9.9 | 10.94 | 245543 | 358901 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 5UW | LL545UW | ll54 5uw | ll545uw | Gwynedd | Gwynedd | Llanfaglan WwTW | 419 | 996 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.56 | 9.9 | 10.94 | 246398 | 359019 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 6TF | LL546TF | ll54 6tf | ll546tf | Gwynedd | Gwynedd | Rhyd Ddu STW | 198 | 2457 | Over1500 | 4.92 | 3.6 | 2.64 | 45.79 | 24.42 | 26.99 | 256952 | 352908 | Snowdonia National Park LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park
LL54 6TG | LL546TG | ll54 6tg | ll546tg | Gwynedd | Gwynedd | Rhyd Ddu STW | 238 | 2457 | Over1500 | 4.92 | 3.6 | 2.64 | 45.79 | 24.42 | 26.99 | 256935 | 352872 | Snowdonia National Park LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park
LL54 6TH | LL546TH | ll54 6th | ll546th | Gwynedd | Gwynedd | Rhyd Ddu STW | 295 | 2457 | Over1500 | 4.92 | 3.6 | 2.64 | 45.79 | 24.42 | 26.99 | 256924 | 352813 | Snowdonia National Park LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park
LL54 6TL | LL546TL | ll54 6tl | ll546tl | Gwynedd | Gwynedd | Rhyd Ddu STW | 255 | 2457 | Over1500 | 4.92 | 3.6 | 2.64 | 45.79 | 24.42 | 26.99 | 256914 | 352864 | Snowdonia National Park LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park
LL54 6TN | LL546TN | ll54 6tn | ll546tn | Gwynedd | Gwynedd | Rhyd Ddu STW | 372 | 2457 | Over1500 | 4.92 | 3.6 | 2.64 | 45.79 | 24.42 | 26.99 | 257025 | 352709 | Snowdonia National Park LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park
LL54 6TP | LL546TP | ll54 6tp | ll546tp | Gwynedd | Gwynedd | Rhyd Ddu STW | 208 | 2457 | Over1500 | 4.92 | 3.6 | 2.64 | 45.79 | 24.42 | 26.99 | 256907 | 352929 | Snowdonia National Park LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park
LL54 7AJ | LL547AJ | ll54 7aj | ll547aj | Gwynedd | Gwynedd | Waunfawr STW | 1027 | 1708 | Over1500 | 3.42 | 2.5 | 1.83 | 31.83 | 16.98 | 18.77 | 253057 | 357970 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7AQ | LL547AQ | ll54 7aq | ll547aq | Gwynedd | Gwynedd | Betws Garmon WwTW | 955 | 1822 | Over1500 | 3.65 | 2.67 | 1.96 | 33.96 | 18.11 | 20.02 | 253371 | 357000 | Snowdonia National Park LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park
LL54 7AX | LL547AX | ll54 7ax | ll547ax | Gwynedd | Gwynedd | Waunfawr STW | 1207 | 1570 | Over1500 | 3.14 | 2.3 | 1.69 | 29.26 | 15.61 | 17.25 | 251683 | 358772 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7BJ | LL547BJ | ll54 7bj | ll547bj | Gwynedd | Gwynedd | Waunfawr STW | 710 | 1570 | Over1500 | 3.14 | 2.3 | 1.69 | 29.26 | 15.61 | 17.25 | 252182 | 358814 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7BQ | LL547BQ | ll54 7bq | ll547bq | Gwynedd | Gwynedd | Waunfawr STW | 1229 | 1570 | Over1500 | 3.14 | 2.3 | 1.69 | 29.26 | 15.61 | 17.25 | 251712 | 358574 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7PN | LL547PN | ll54 7pn | ll547pn | Gwynedd | Gwynedd | Waunfawr STW | 2422 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 250456 | 359141 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7UN | LL547UN | ll54 7un | ll547un | Gwynedd | Gwynedd | Llanfaglan WwTW | 1681 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248240 | 359839 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7UP | LL547UP | ll54 7up | ll547up | Gwynedd | Gwynedd | Llanfaglan WwTW | 1728 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248329 | 359661 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7UR | LL547UR | ll54 7ur | ll547ur | Gwynedd | Gwynedd | Llanfaglan WwTW | 1771 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248364 | 359709 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7UT | LL547UT | ll54 7ut | ll547ut | Gwynedd | Gwynedd | Llanfaglan WwTW | 1820 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248420 | 359676 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7UW | LL547UW | ll54 7uw | ll547uw | Gwynedd | Gwynedd | Llanfaglan WwTW | 1662 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248257 | 359686 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7YE | LL547YE | ll54 7ye | ll547ye | Gwynedd | Gwynedd | Llanfaglan WwTW | 2288 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 248898 | 359639 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7YF | LL547YF | ll54 7yf | ll547yf | Gwynedd | Gwynedd | Llanfaglan WwTW | 1557 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 248180 | 359279 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7YG | LL547YG | ll54 7yg | ll547yg | Gwynedd | Gwynedd | Llanfaglan WwTW | 1706 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 248265 | 358896 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7YH | LL547YH | ll54 7yh | ll547yh | Gwynedd | Gwynedd | Llanfaglan WwTW | 1510 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 248068 | 358921 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7YJ | LL547YJ | ll54 7yj | ll547yj | Gwynedd | Gwynedd | Llanfaglan WwTW | 1482 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 248019 | 358866 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL54 7YR | LL547YR | ll54 7yr | ll547yr | Gwynedd | Gwynedd | Betws Garmon WwTW | 201 | 1840 | Over1500 | 3.68 | 2.69 | 1.98 | 34.29 | 18.29 | 20.22 | 254491 | 356742 | Snowdonia National Park LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park
LL54 7YS | LL547YS | ll54 7ys | ll547ys | Gwynedd | Gwynedd | Rhyd Ddu STW | 1054 | 2360 | Over1500 | 4.72 | 3.46 | 2.53 | 43.99 | 23.46 | 25.93 | 257122 | 354131 | Snowdonia National Park LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park
LL54 7YT | LL547YT | ll54 7yt | ll547yt | Gwynedd | Gwynedd | Betws Garmon WwTW | 1121 | 2297 | Over1500 | 4.6 | 3.36 | 2.47 | 42.81 | 22.83 | 25.24 | 255123 | 355990 | Snowdonia National Park LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park
LL54 7YU | LL547YU | ll54 7yu | ll547yu | Gwynedd | Gwynedd | Betws Garmon WwTW | 268 | 1840 | Over1500 | 3.68 | 2.69 | 1.98 | 34.29 | 18.29 | 20.22 | 254042 | 356842 | Snowdonia National Park LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park
LL54 7YY | LL547YY | ll54 7yy | ll547yy | Gwynedd | Gwynedd | Betws Garmon WwTW | 775 | 1840 | Over1500 | 3.68 | 2.69 | 1.98 | 34.29 | 18.29 | 20.22 | 253834 | 357366 | Snowdonia National Park LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Parc Cenedlaethol Eryri | Eryri National Park
LL55 2EZ | LL552EZ | ll55 2ez | ll552ez | Gwynedd | Gwynedd | Llanfaglan WwTW | 1618 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248060 | 360119 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2SS | LL552SS | ll55 2ss | ll552ss | Gwynedd | Gwynedd | Waunfawr STW | 3769 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 250211 | 361648 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2ST | LL552ST | ll55 2st | ll552st | Gwynedd | Gwynedd | Waunfawr STW | 3332 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 250360 | 361169 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2SY | LL552SY | ll55 2sy | ll552sy | Gwynedd | Gwynedd | Waunfawr STW | 3916 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 250015 | 361658 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2TA | LL552TA | ll55 2ta | ll552ta | Gwynedd | Gwynedd | Waunfawr STW | 3900 | 1122 | 900to1200 | 2.25 | 1.64 | 1.21 | 20.91 | 11.15 | 12.33 | 249901 | 361506 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2TB | LL552TB | ll55 2tb | ll552tb | Gwynedd | Gwynedd | Llanfaglan WwTW | 3445 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 249674 | 360975 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2TD | LL552TD | ll55 2td | ll552td | Gwynedd | Gwynedd | Llanfaglan WwTW | 3252 | 1132 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.1 | 11.25 | 12.44 | 249301 | 361218 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2TE | LL552TE | ll55 2te | ll552te | Gwynedd | Gwynedd | Llanfaglan WwTW | 2891 | 1132 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.1 | 11.25 | 12.44 | 249038 | 360964 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2TF | LL552TF | ll55 2tf | ll552tf | Gwynedd | Gwynedd | Llanfaglan WwTW | 2930 | 1132 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.1 | 11.25 | 12.44 | 249188 | 360790 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2TG | LL552TG | ll55 2tg | ll552tg | Gwynedd | Gwynedd | Waunfawr STW | 3198 | 1260 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.48 | 12.53 | 13.84 | 249999 | 360384 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2TH | LL552TH | ll55 2th | ll552th | Gwynedd | Gwynedd | Llanfaglan WwTW | 2977 | 1132 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.1 | 11.25 | 12.44 | 249231 | 360810 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2TL | LL552TL | ll55 2tl | ll552tl | Gwynedd | Gwynedd | Waunfawr STW | 2771 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 251231 | 361212 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2TY | LL552TY | ll55 2ty | ll552ty | Gwynedd | Gwynedd | Llanfaglan WwTW | 2038 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248373 | 360419 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2UA | LL552UA | ll55 2ua | ll552ua | Gwynedd | Gwynedd | Llanfaglan WwTW | 1905 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248321 | 360240 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2UB | LL552UB | ll55 2ub | ll552ub | Gwynedd | Gwynedd | Llanfaglan WwTW | 1756 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248196 | 360157 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2UD | LL552UD | ll55 2ud | ll552ud | Gwynedd | Gwynedd | Llanfaglan WwTW | 1656 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248053 | 360209 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2UE | LL552UE | ll55 2ue | ll552ue | Gwynedd | Gwynedd | Llanfaglan WwTW | 1743 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248232 | 360048 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2UF | LL552UF | ll55 2uf | ll552uf | Gwynedd | Gwynedd | Llanfaglan WwTW | 1732 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248254 | 359962 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2UG | LL552UG | ll55 2ug | ll552ug | Gwynedd | Gwynedd | Llanfaglan WwTW | 1755 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248296 | 359909 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2UH | LL552UH | ll55 2uh | ll552uh | Gwynedd | Gwynedd | Llanfaglan WwTW | 1843 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248340 | 360046 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2UL | LL552UL | ll55 2ul | ll552ul | Gwynedd | Gwynedd | Llanfaglan WwTW | 1874 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248385 | 360015 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2UN | LL552UN | ll55 2un | ll552un | Gwynedd | Gwynedd | Llanfaglan WwTW | 1907 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248430 | 359989 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2UW | LL552UW | ll55 2uw | ll552uw | Gwynedd | Gwynedd | Llanfaglan WwTW | 1567 | 1081 | 900to1200 | 2.16 | 1.58 | 1.16 | 20.15 | 10.75 | 11.88 | 248061 | 360000 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 2YA | LL552YA | ll55 2ya | ll552ya | Gwynedd | Gwynedd | Llanfaglan WwTW | 2174 | 1158 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.58 | 11.51 | 12.72 | 248658 | 360143 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4AJ | LL554AJ | ll55 4aj | ll554aj | Gwynedd | Gwynedd | Waunfawr STW | 399 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 252575 | 359246 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4AQ | LL554AQ | ll55 4aq | ll554aq | Gwynedd | Gwynedd | Waunfawr STW | 298 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 252674 | 358758 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4AX | LL554AX | ll55 4ax | ll554ax | Gwynedd | Gwynedd | Waunfawr STW | 170 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 253023 | 359057 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4AZ | LL554AZ | ll55 4az | ll554az | Gwynedd | Gwynedd | Waunfawr STW | 355 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 252673 | 359274 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4BJ | LL554BJ | ll55 4bj | ll554bj | Gwynedd | Gwynedd | Waunfawr STW | 292 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 252843 | 359271 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4BQ | LL554BQ | ll55 4bq | ll554bq | Gwynedd | Gwynedd | Waunfawr STW | 207 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 252818 | 359180 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4BX | LL554BX | ll55 4bx | ll554bx | Gwynedd | Gwynedd | Waunfawr STW | 475 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 252882 | 359455 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4BZ | LL554BZ | ll55 4bz | ll554bz | Gwynedd | Gwynedd | Waunfawr STW | 590 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 253171 | 359489 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4DJ | LL554DJ | ll55 4dj | ll554dj | Gwynedd | Gwynedd | Waunfawr STW | 929 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 252275 | 359692 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4DQ | LL554DQ | ll55 4dq | ll554dq | Gwynedd | Gwynedd | Waunfawr STW | 860 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 252334 | 359651 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4DX | LL554DX | ll55 4dx | ll554dx | Gwynedd | Gwynedd | Waunfawr STW | 922 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 252375 | 359756 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4DZ | LL554DZ | ll55 4dz | ll554dz | Gwynedd | Gwynedd | Waunfawr STW | 919 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 252634 | 359868 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4EJ | LL554EJ | ll55 4ej | ll554ej | Gwynedd | Gwynedd | Waunfawr STW | 1116 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 252923 | 360095 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4EQ | LL554EQ | ll55 4eq | ll554eq | Gwynedd | Gwynedd | Waunfawr STW | 1066 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 252735 | 360037 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4EX | LL554EX | ll55 4ex | ll554ex | Gwynedd | Gwynedd | Waunfawr STW | 1024 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 253429 | 359839 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4EZ | LL554EZ | ll55 4ez | ll554ez | Gwynedd | Gwynedd | Waunfawr STW | 1271 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 252203 | 360060 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4HQ | LL554HQ | ll55 4hq | ll554hq | Gwynedd | Gwynedd | Waunfawr STW | 2443 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 251064 | 360623 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4LJ | LL554LJ | ll55 4lj | ll554lj | Gwynedd | Gwynedd | Waunfawr STW | 642 | 1570 | Over1500 | 3.14 | 2.3 | 1.69 | 29.26 | 15.61 | 17.25 | 252486 | 359493 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4LQ | LL554LQ | ll55 4lq | ll554lq | Gwynedd | Gwynedd | Waunfawr STW | 719 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 252643 | 359661 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4LX | LL554LX | ll55 4lx | ll554lx | Gwynedd | Gwynedd | Waunfawr STW | 727 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 252409 | 359541 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4LZ | LL554LZ | ll55 4lz | ll554lz | Gwynedd | Gwynedd | Waunfawr STW | 941 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 252228 | 359666 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4PJ | LL554PJ | ll55 4pj | ll554pj | Gwynedd | Gwynedd | Waunfawr STW | 882 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 252243 | 359598 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4PQ | LL554PQ | ll55 4pq | ll554pq | Gwynedd | Gwynedd | Waunfawr STW | 1775 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 251242 | 359682 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4PZ | LL554PZ | ll55 4pz | ll554pz | Gwynedd | Gwynedd | Waunfawr STW | 286 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 252737 | 359232 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4SA | LL554SA | ll55 4sa | ll554sa | Gwynedd | Gwynedd | Waunfawr STW | 2076 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 253152 | 361037 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4SB | LL554SB | ll55 4sb | ll554sb | Gwynedd | Gwynedd | Waunfawr STW | 1256 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 252900 | 360236 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4SD | LL554SD | ll55 4sd | ll554sd | Gwynedd | Gwynedd | Waunfawr STW | 1340 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 252715 | 360311 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4YP | LL554YP | ll55 4yp | ll554yp | Gwynedd | Gwynedd | Waunfawr STW | 1257 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 251957 | 359841 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4YR | LL554YR | ll55 4yr | ll554yr | Gwynedd | Gwynedd | Waunfawr STW | 1798 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 251477 | 360114 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4YS | LL554YS | ll55 4ys | ll554ys | Gwynedd | Gwynedd | Waunfawr STW | 1114 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 252030 | 359709 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4YT | LL554YT | ll55 4yt | ll554yt | Gwynedd | Gwynedd | Waunfawr STW | 994 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 252112 | 359621 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4YU | LL554YU | ll55 4yu | ll554yu | Gwynedd | Gwynedd | Waunfawr STW | 355 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 252575 | 359175 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4YX | LL554YX | ll55 4yx | ll554yx | Gwynedd | Gwynedd | Waunfawr STW | 680 | 1570 | Over1500 | 3.14 | 2.3 | 1.69 | 29.26 | 15.61 | 17.25 | 252351 | 359417 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4YY | LL554YY | ll55 4yy | ll554yy | Gwynedd | Gwynedd | Waunfawr STW | 643 | 1570 | Over1500 | 3.14 | 2.3 | 1.69 | 29.26 | 15.61 | 17.25 | 252381 | 359395 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
LL55 4ZA | LL554ZA | ll55 4za | ll554za | Gwynedd | Gwynedd | Waunfawr STW | 576 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 252502 | 359422 | Gwynedd LPA | NW | Afon Gwyrfai a Llyn Cwellyn | Cyngor Gwynedd | Gwynedd Council
SA33 6AT | SA336AT | sa33 6at | sa336at | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 3155 | 1808 | Over1500 | 3.62 | 2.65 | 1.94 | 33.7 | 17.97 | 19.86 | 236980 | 233792 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6AU | SA336AU | sa33 6au | sa336au | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 4847 | 1720 | Over1500 | 3.44 | 2.52 | 1.85 | 32.06 | 17.1 | 18.9 | 235027 | 234723 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6RL | SA336RL | sa33 6rl | sa336rl | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 3759 | 1756 | Over1500 | 3.51 | 2.57 | 1.89 | 32.73 | 17.46 | 19.29 | 230201 | 232388 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6RN | SA336RN | sa33 6rn | sa336rn | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 2930 | 1682 | Over1500 | 3.37 | 2.46 | 1.81 | 31.35 | 16.72 | 18.48 | 229820 | 233155 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6RP | SA336RP | sa33 6rp | sa336rp | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 3571 | 1754 | Over1500 | 3.51 | 2.57 | 1.88 | 32.69 | 17.44 | 19.27 | 228973 | 232485 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TG | SA336TG | sa33 6tg | sa336tg | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 4476 | 1835 | Over1500 | 3.67 | 2.69 | 1.97 | 34.2 | 18.24 | 20.16 | 231808 | 232326 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA35 0AA | SA350AA | sa35 0aa | sa350aa | Pembrokeshire | Sir Benfro | Capel Iwan STW | 1525 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 228077 | 235142 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AB | SA350AB | sa35 0ab | sa350ab | Pembrokeshire | Sir Benfro | Capel Iwan STW | 2383 | 1589 | Over1500 | 3.18 | 2.33 | 1.71 | 29.62 | 15.8 | 17.46 | 228228 | 233917 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AD | SA350AD | sa35 0ad | sa350ad | Pembrokeshire | Sir Benfro | Capel Iwan STW | 3272 | 1738 | Over1500 | 3.48 | 2.55 | 1.87 | 32.39 | 17.28 | 19.1 | 228691 | 232827 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AE | SA350AE | sa35 0ae | sa350ae | Pembrokeshire | Sir Benfro | Capel Iwan STW | 3460 | 1686 | Over1500 | 3.37 | 2.47 | 1.81 | 31.42 | 16.76 | 18.52 | 227725 | 232965 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AG | SA350AG | sa35 0ag | sa350ag | Pembrokeshire | Sir Benfro | Capel Iwan STW | 4169 | 1697 | Over1500 | 3.4 | 2.49 | 1.82 | 31.63 | 16.87 | 18.64 | 227511 | 232279 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AH | SA350AH | sa35 0ah | sa350ah | Pembrokeshire | Sir Benfro | Capel Iwan STW | 4984 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 225317 | 233057 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AJ | SA350AJ | sa35 0aj | sa350aj | Pembrokeshire | Sir Benfro | Capel Iwan STW | 5260 | 1700 | Over1500 | 3.4 | 2.49 | 1.83 | 31.69 | 16.9 | 18.68 | 225488 | 232426 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AL | SA350AL | sa35 0al | sa350al | Pembrokeshire | Sir Benfro | Capel Iwan STW | 4442 | 1618 | Over1500 | 3.24 | 2.37 | 1.74 | 30.16 | 16.08 | 17.78 | 225319 | 234091 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AN | SA350AN | sa35 0an | sa350an | Pembrokeshire | Sir Benfro | Capel Iwan STW | 4609 | 1563 | Over1500 | 3.13 | 2.29 | 1.68 | 29.13 | 15.54 | 17.17 | 224916 | 234649 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AP | SA350AP | sa35 0ap | sa350ap | Pembrokeshire | Sir Benfro | Newchapel STW | 3878 | 1516 | Over1500 | 3.03 | 2.22 | 1.63 | 28.26 | 15.07 | 16.66 | 224026 | 235528 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AQ | SA350AQ | sa35 0aq | sa350aq | Pembrokeshire | Sir Benfro | Capel Iwan STW | 4323 | 1635 | Over1500 | 3.27 | 2.39 | 1.76 | 30.47 | 16.25 | 17.96 | 226302 | 232936 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AR | SA350AR | sa35 0ar | sa350ar | Pembrokeshire | Sir Benfro | Capel Iwan STW | 4332 | 1563 | Over1500 | 3.13 | 2.29 | 1.68 | 29.13 | 15.54 | 17.17 | 225020 | 235440 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AS | SA350AS | sa35 0as | sa350as | Pembrokeshire | Sir Benfro | Capel Iwan STW | 3814 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 226343 | 233643 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AT | SA350AT | sa35 0at | sa350at | Pembrokeshire | Sir Benfro | Capel Iwan STW | 3081 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 226627 | 234525 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AU | SA350AU | sa35 0au | sa350au | Pembrokeshire | Sir Benfro | Capel Iwan STW | 3166 | 1553 | Over1500 | 3.11 | 2.27 | 1.67 | 28.95 | 15.44 | 17.06 | 226197 | 235461 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AW | SA350AW | sa35 0aw | sa350aw | Pembrokeshire | Sir Benfro | Newchapel STW | 4594 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 224496 | 234957 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0AX | SA350AX | sa35 0ax | sa350ax | Pembrokeshire | Sir Benfro | Capel Iwan STW | 2095 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 227233 | 235768 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0BE | SA350BE | sa35 0be | sa350be | Pembrokeshire | Sir Benfro | Newchapel STW | 6141 | 1654 | Over1500 | 3.31 | 2.42 | 1.78 | 30.83 | 16.44 | 18.17 | 223135 | 232975 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0BH | SA350BH | sa35 0bh | sa350bh | Pembrokeshire | Sir Benfro | Capel Iwan STW | 5844 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 224544 | 232659 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0BL | SA350BL | sa35 0bl | sa350bl | Pembrokeshire | Sir Benfro | Newchapel STW | 5814 | 1654 | Over1500 | 3.31 | 2.42 | 1.78 | 30.83 | 16.44 | 18.17 | 222778 | 233274 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0BP | SA350BP | sa35 0bp | sa350bp | Pembrokeshire | Sir Benfro | Newchapel STW | 4315 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 223887 | 235004 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0BS | SA350BS | sa35 0bs | sa350bs | Pembrokeshire | Sir Benfro | Newchapel STW | 5316 | 1664 | Over1500 | 3.33 | 2.44 | 1.79 | 31.01 | 16.54 | 18.28 | 223041 | 233795 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0BT | SA350BT | sa35 0bt | sa350bt | Pembrokeshire | Sir Benfro | Newchapel STW | 5886 | 1648 | Over1500 | 3.3 | 2.41 | 1.77 | 30.72 | 16.38 | 18.11 | 223894 | 233369 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0DN | SA350DN | sa35 0dn | sa350dn | Pembrokeshire | Sir Benfro | Newchapel STW | 3675 | 1640 | Over1500 | 3.28 | 2.4 | 1.76 | 30.57 | 16.3 | 18.02 | 223036 | 235449 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0DP | SA350DP | sa35 0dp | sa350dp | Pembrokeshire | Sir Benfro | Newchapel STW | 3424 | 1516 | Over1500 | 3.03 | 2.22 | 1.63 | 28.26 | 15.07 | 16.66 | 224111 | 236075 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA35 0DW | SA350DW | sa35 0dw | sa350dw | Pembrokeshire | Sir Benfro | Newchapel STW | 3304 | 1554 | Over1500 | 3.11 | 2.28 | 1.67 | 28.96 | 15.45 | 17.07 | 223372 | 235902 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0AB | SA370AB | sa37 0ab | sa370ab | Pembrokeshire | Sir Benfro | Boncath STW | 655 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 220123 | 238385 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0EH | SA370EH | sa37 0eh | sa370eh | Pembrokeshire | Sir Benfro | Newchapel STW | 605 | 1341 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.99 | 13.33 | 14.73 | 222915 | 239490 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0EL | SA370EL | sa37 0el | sa370el | Pembrokeshire | Sir Benfro | Newchapel STW | 1272 | 1312 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.45 | 13.04 | 14.41 | 223108 | 237980 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0EN | SA370EN | sa37 0en | sa370en | Pembrokeshire | Sir Benfro | Newchapel STW | 900 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 221570 | 239089 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0EP | SA370EP | sa37 0ep | sa370ep | Pembrokeshire | Sir Benfro | Boncath STW | 1261 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 221296 | 238586 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0ER | SA370ER | sa37 0er | sa370er | Pembrokeshire | Sir Benfro | Newchapel STW | 1239 | 1232 | 1200to1500 | 2.47 | 1.8 | 1.32 | 22.96 | 12.25 | 13.54 | 221348 | 239606 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0ES | SA370ES | sa37 0es | sa370es | Pembrokeshire | Sir Benfro | Newchapel STW | 1075 | 1294 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.12 | 12.86 | 14.22 | 222551 | 240152 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0ET | SA370ET | sa37 0et | sa370et | Pembrokeshire | Sir Benfro | Abercych WwTW | 1113 | 1171 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.83 | 11.64 | 12.87 | 223239 | 241113 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0EU | SA370EU | sa37 0eu | sa370eu | Pembrokeshire | Sir Benfro | Abercych WwTW | 544 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 224095 | 241690 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0EW | SA370EW | sa37 0ew | sa370ew | Pembrokeshire | Sir Benfro | Newchapel STW | 382 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 222211 | 238799 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0EX | SA370EX | sa37 0ex | sa370ex | Pembrokeshire | Sir Benfro | Abercych WwTW | 403 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 224716 | 241043 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0EY | SA370EY | sa37 0ey | sa370ey | Pembrokeshire | Sir Benfro | Abercych WwTW | 670 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 224891 | 240816 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0EZ | SA370EZ | sa37 0ez | sa370ez | Pembrokeshire | Sir Benfro | Abercych WwTW | 816 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 224968 | 240678 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HA | SA370HA | sa37 0ha | sa370ha | Pembrokeshire | Sir Benfro | Abercych WwTW | 1070 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 224985 | 240348 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HB | SA370HB | sa37 0hb | sa370hb | Pembrokeshire | Sir Benfro | Abercych WwTW | 1194 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 224973 | 240191 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HD | SA370HD | sa37 0hd | sa370hd | Pembrokeshire | Sir Benfro | Abercych WwTW | 1243 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 224893 | 240091 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HE | SA370HE | sa37 0he | sa370he | Pembrokeshire | Sir Benfro | Abercych WwTW | 1025 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 224609 | 240217 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HF | SA370HF | sa37 0hf | sa370hf | Pembrokeshire | Sir Benfro | Abercych WwTW | 1473 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 224140 | 239750 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HG | SA370HG | sa37 0hg | sa370hg | Pembrokeshire | Sir Benfro | Newchapel STW | 1005 | 1341 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.99 | 13.33 | 14.73 | 223431 | 239375 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HH | SA370HH | sa37 0hh | sa370hh | Pembrokeshire | Sir Benfro | Abercych WwTW | 1175 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 223560 | 240336 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HJ | SA370HJ | sa37 0hj | sa370hj | Pembrokeshire | Sir Benfro | Abercych WwTW | 1389 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 225031 | 239999 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HL | SA370HL | sa37 0hl | sa370hl | Pembrokeshire | Sir Benfro | Abercych WwTW | 1258 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 224915 | 240085 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HQ | SA370HQ | sa37 0hq | sa370hq | Pembrokeshire | Sir Benfro | Newchapel STW | 1926 | 1368 | 1200to1500 | 2.74 | 2 | 1.47 | 25.5 | 13.6 | 15.03 | 224234 | 238308 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HR | SA370HR | sa37 0hr | sa370hr | Pembrokeshire | Sir Benfro | Boncath STW | 725 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 220111 | 238315 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HS | SA370HS | sa37 0hs | sa370hs | Pembrokeshire | Sir Benfro | Boncath STW | 155 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 220071 | 239187 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0HY | SA370HY | sa37 0hy | sa370hy | Pembrokeshire | Sir Benfro | Boncath STW | 2655 | 1587 | Over1500 | 3.18 | 2.32 | 1.7 | 29.58 | 15.78 | 17.44 | 218994 | 236636 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JG | SA370JG | sa37 0jg | sa370jg | Pembrokeshire | Sir Benfro | Boncath STW | 1365 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 220053 | 237677 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JH | SA370JH | sa37 0jh | sa370jh | Pembrokeshire | Sir Benfro | Boncath STW | 2804 | 1587 | Over1500 | 3.18 | 2.32 | 1.7 | 29.58 | 15.78 | 17.44 | 218902 | 236514 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JL | SA370JL | sa37 0jl | sa370jl | Pembrokeshire | Sir Benfro | Boncath STW | 846 | 1458 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.17 | 14.49 | 16.02 | 220666 | 238394 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JN | SA370JN | sa37 0jn | sa370jn | Pembrokeshire | Sir Benfro | Boncath STW | 754 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 220457 | 238365 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JP | SA370JP | sa37 0jp | sa370jp | Pembrokeshire | Sir Benfro | Boncath STW | 909 | 1458 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.17 | 14.49 | 16.02 | 220530 | 238229 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JQ | SA370JQ | sa37 0jq | sa370jq | Pembrokeshire | Sir Benfro | Boncath STW | 452 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 220326 | 238638 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JR | SA370JR | sa37 0jr | sa370jr | Pembrokeshire | Sir Benfro | Newchapel STW | 1921 | 1501 | Over1500 | 3 | 2.2 | 1.61 | 27.98 | 14.92 | 16.49 | 221432 | 237464 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JS | SA370JS | sa37 0js | sa370js | Pembrokeshire | Sir Benfro | Newchapel STW | 3240 | 1557 | Over1500 | 3.12 | 2.28 | 1.67 | 29.02 | 15.48 | 17.11 | 221725 | 235927 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JT | SA370JT | sa37 0jt | sa370jt | Pembrokeshire | Sir Benfro | Newchapel STW | 3372 | 1554 | Over1500 | 3.11 | 2.28 | 1.67 | 28.96 | 15.45 | 17.07 | 222645 | 235713 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JU | SA370JU | sa37 0ju | sa370ju | Pembrokeshire | Sir Benfro | Newchapel STW | 3296 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 224833 | 236783 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JW | SA370JW | sa37 0jw | sa370jw | Pembrokeshire | Sir Benfro | Boncath STW | 576 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 220365 | 238519 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JX | SA370JX | sa37 0jx | sa370jx | Pembrokeshire | Sir Benfro | Newchapel STW | 2835 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 224712 | 237345 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JY | SA370JY | sa37 0jy | sa370jy | Pembrokeshire | Sir Benfro | Newchapel STW | 2683 | 1389 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.89 | 13.81 | 15.26 | 223929 | 236828 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0JZ | SA370JZ | sa37 0jz | sa370jz | Pembrokeshire | Sir Benfro | Newchapel STW | 2625 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 223041 | 236518 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0LA | SA370LA | sa37 0la | sa370la | Pembrokeshire | Sir Benfro | Boncath STW | 1625 | 1458 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.17 | 14.49 | 16.02 | 220661 | 237508 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0LG | SA370LG | sa37 0lg | sa370lg | Carmarthenshire | Sir Gaerfyrddin | Abercych WwTW | 1436 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 225161 | 240024 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA37 0LH | SA370LH | sa37 0lh | sa370lh | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 3230 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 226639 | 238409 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA37 0LJ | SA370LJ | sa37 0lj | sa370lj | Pembrokeshire | Sir Benfro | Abercych WwTW | 3098 | 1281 | 1200to1500 | 2.56 | 1.88 | 1.38 | 23.88 | 12.73 | 14.07 | 225727 | 238434 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0LL | SA370LL | sa37 0ll | sa370ll | Pembrokeshire | Sir Benfro | Capel Iwan STW | 2844 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 226953 | 237632 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0LN | SA370LN | sa37 0ln | sa370ln | Pembrokeshire | Sir Benfro | Newchapel STW | 3532 | 1281 | 1200to1500 | 2.56 | 1.88 | 1.38 | 23.88 | 12.73 | 14.07 | 225755 | 237782 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA37 0LQ | SA370LQ | sa37 0lq | sa370lq | Carmarthenshire | Sir Gaerfyrddin | Abercych WwTW | 2616 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 225758 | 239005 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA37 0LW | SA370LW | sa37 0lw | sa370lw | Pembrokeshire | Sir Benfro | Capel Iwan STW | 3264 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 226089 | 236566 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA38 9AA | SA389AA | sa38 9aa | sa389aa | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 389 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230877 | 240735 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AB | SA389AB | sa38 9ab | sa389ab | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 310 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230788 | 240711 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AE | SA389AE | sa38 9ae | sa389ae | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 411 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230898 | 240730 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AF | SA389AF | sa38 9af | sa389af | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 456 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230946 | 240743 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AG | SA389AG | sa38 9ag | sa389ag | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 453 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230940 | 240724 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AJ | SA389AJ | sa38 9aj | sa389aj | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 377 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230815 | 240614 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AN | SA389AN | sa38 9an | sa389an | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 391 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230733 | 240503 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AP | SA389AP | sa38 9ap | sa389ap | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 363 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230824 | 240659 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AQ | SA389AQ | sa38 9aq | sa389aq | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 420 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230900 | 240698 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AR | SA389AR | sa38 9ar | sa389ar | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 316 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230762 | 240643 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AS | SA389AS | sa38 9as | sa389as | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 380 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230745 | 240527 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AU | SA389AU | sa38 9au | sa389au | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 354 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230767 | 240586 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AW | SA389AW | sa38 9aw | sa389aw | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 386 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230737 | 240513 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AX | SA389AX | sa38 9ax | sa389ax | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 625 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 229922 | 241061 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AY | SA389AY | sa38 9ay | sa389ay | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 621 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 229912 | 241026 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9AZ | SA389AZ | sa38 9az | sa389az | Ceredigion | Sir Ceredigion | Adpar WwTW | 970 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 231457 | 240946 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9BA | SA389BA | sa38 9ba | sa389ba | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 214 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230563 | 240611 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BD | SA389BD | sa38 9bd | sa389bd | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 476 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230970 | 240768 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BE | SA389BE | sa38 9be | sa389be | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 331 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230576 | 240493 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BG | SA389BG | sa38 9bg | sa389bg | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 370 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230691 | 240499 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BH | SA389BH | sa38 9bh | sa389bh | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 465 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230738 | 240417 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BJ | SA389BJ | sa38 9bj | sa389bj | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 480 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230771 | 240421 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BL | SA389BL | sa38 9bl | sa389bl | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1126 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 231525 | 240357 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BN | SA389BN | sa38 9bn | sa389bn | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 556 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230839 | 240377 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BP | SA389BP | sa38 9bp | sa389bp | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 642 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230936 | 240347 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BQ | SA389BQ | sa38 9bq | sa389bq | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 421 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230729 | 240463 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BR | SA389BR | sa38 9br | sa389br | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 680 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231005 | 240363 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BS | SA389BS | sa38 9bs | sa389bs | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 675 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230960 | 240324 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BT | SA389BT | sa38 9bt | sa389bt | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 752 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231070 | 240328 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BU | SA389BU | sa38 9bu | sa389bu | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 777 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231101 | 240326 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BW | SA389BW | sa38 9bw | sa389bw | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 565 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230799 | 240337 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BX | SA389BX | sa38 9bx | sa389bx | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 933 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231311 | 240359 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BY | SA389BY | sa38 9by | sa389by | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1006 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231415 | 240406 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9BZ | SA389BZ | sa38 9bz | sa389bz | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1121 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 231568 | 240486 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DA | SA389DA | sa38 9da | sa389da | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1362 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 231846 | 240636 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DB | SA389DB | sa38 9db | sa389db | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1142 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 231531 | 240332 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DD | SA389DD | sa38 9dd | sa389dd | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1165 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231499 | 240221 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DE | SA389DE | sa38 9de | sa389de | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1151 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 231559 | 240374 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DF | SA389DF | sa38 9df | sa389df | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 574 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230893 | 240400 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DG | SA389DG | sa38 9dg | sa389dg | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1138 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 231501 | 240280 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DH | SA389DH | sa38 9dh | sa389dh | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1118 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231436 | 240209 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DJ | SA389DJ | sa38 9dj | sa389dj | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1050 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231287 | 240123 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DL | SA389DL | sa38 9dl | sa389dl | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1138 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231427 | 240160 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DN | SA389DN | sa38 9dn | sa389dn | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1147 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231449 | 240176 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DQ | SA389DQ | sa38 9dq | sa389dq | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1372 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 231671 | 240106 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DS | SA389DS | sa38 9ds | sa389ds | Ceredigion | Sir Ceredigion | Adpar WwTW | 467 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230916 | 241017 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9DT | SA389DT | sa38 9dt | sa389dt | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1036 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231333 | 240203 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DU | SA389DU | sa38 9du | sa389du | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 382 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230878 | 240796 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DW | SA389DW | sa38 9dw | sa389dw | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 985 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231287 | 240227 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9DX | SA389DX | sa38 9dx | sa389dx | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 402 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230897 | 240782 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9EA | SA389EA | sa38 9ea | sa389ea | Ceredigion | Sir Ceredigion | Adpar WwTW | 342 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230822 | 240917 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9ED | SA389ED | sa38 9ed | sa389ed | Ceredigion | Sir Ceredigion | Adpar WwTW | 407 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230892 | 240908 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EE | SA389EE | sa38 9ee | sa389ee | Ceredigion | Sir Ceredigion | Adpar WwTW | 445 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230932 | 240904 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EF | SA389EF | sa38 9ef | sa389ef | Ceredigion | Sir Ceredigion | Adpar WwTW | 499 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230993 | 240857 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EG | SA389EG | sa38 9eg | sa389eg | Ceredigion | Sir Ceredigion | Adpar WwTW | 535 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230923 | 241137 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EH | SA389EH | sa38 9eh | sa389eh | Ceredigion | Sir Ceredigion | Adpar WwTW | 457 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230903 | 241021 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EJ | SA389EJ | sa38 9ej | sa389ej | Ceredigion | Sir Ceredigion | Adpar WwTW | 479 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230947 | 240974 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EL | SA389EL | sa38 9el | sa389el | Ceredigion | Sir Ceredigion | Adpar WwTW | 699 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230968 | 241329 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EN | SA389EN | sa38 9en | sa389en | Ceredigion | Sir Ceredigion | Adpar WwTW | 1078 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 231112 | 241698 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EP | SA389EP | sa38 9ep | sa389ep | Ceredigion | Sir Ceredigion | Adpar WwTW | 3071 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 232666 | 242987 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EQ | SA389EQ | sa38 9eq | sa389eq | Ceredigion | Sir Ceredigion | Adpar WwTW | 974 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 231451 | 241004 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9ER | SA389ER | sa38 9er | sa389er | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3407 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 232805 | 244415 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9ES | SA389ES | sa38 9es | sa389es | Ceredigion | Sir Ceredigion | Beulah WwTW | 2586 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 231959 | 245423 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9ET | SA389ET | sa38 9et | sa389et | Ceredigion | Sir Ceredigion | Beulah WwTW | 2782 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 232125 | 245297 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EU | SA389EU | sa38 9eu | sa389eu | Ceredigion | Sir Ceredigion | Beulah WwTW | 2736 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 231786 | 244687 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EW | SA389EW | sa38 9ew | sa389ew | Ceredigion | Sir Ceredigion | Adpar WwTW | 2244 | 1222 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.78 | 12.15 | 13.43 | 232141 | 242340 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EX | SA389EX | sa38 9ex | sa389ex | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2632 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 232816 | 245373 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9EY | SA389EY | sa38 9ey | sa389ey | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2087 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 233950 | 245329 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9HA | SA389HA | sa38 9ha | sa389ha | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2377 | 1140 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.25 | 11.33 | 12.53 | 232675 | 245912 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9HB | SA389HB | sa38 9hb | sa389hb | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 2447 | 1208 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.52 | 12.01 | 13.27 | 233232 | 241541 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9HD | SA389HD | sa38 9hd | sa389hd | Ceredigion | Sir Ceredigion | Adpar WwTW | 2052 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 232458 | 241414 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9HH | SA389HH | sa38 9hh | sa389hh | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 426 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230678 | 240429 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HJ | SA389HJ | sa38 9hj | sa389hj | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 433 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230642 | 240406 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HL | SA389HL | sa38 9hl | sa389hl | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 501 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230704 | 240358 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HN | SA389HN | sa38 9hn | sa389hn | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 492 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230738 | 240386 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HP | SA389HP | sa38 9hp | sa389hp | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 675 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230815 | 240219 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HQ | SA389HQ | sa38 9hq | sa389hq | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1279 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231139 | 239709 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HR | SA389HR | sa38 9hr | sa389hr | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 774 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230909 | 240159 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HS | SA389HS | sa38 9hs | sa389hs | Carmarthenshire | Sir Gaerfyrddin | Drefach/Velindre WwTW | 2187 | 1228 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.89 | 12.21 | 13.49 | 233169 | 240585 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HT | SA389HT | sa38 9ht | sa389ht | Carmarthenshire | Sir Gaerfyrddin | Drefach/Velindre WwTW | 1540 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 233799 | 240385 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HU | SA389HU | sa38 9hu | sa389hu | Carmarthenshire | Sir Gaerfyrddin | Drefach/Velindre WwTW | 1278 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 234066 | 240431 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HW | SA389HW | sa38 9hw | sa389hw | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 814 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231005 | 240179 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HX | SA389HX | sa38 9hx | sa389hx | Carmarthenshire | Sir Gaerfyrddin | Drefach/Velindre WwTW | 1398 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 233938 | 240259 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HY | SA389HY | sa38 9hy | sa389hy | Carmarthenshire | Sir Gaerfyrddin | Drefach/Velindre WwTW | 1370 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 233976 | 240123 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9HZ | SA389HZ | sa38 9hz | sa389hz | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 851 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 231024 | 240147 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9JA | SA389JA | sa38 9ja | sa389ja | Carmarthenshire | Sir Gaerfyrddin | Drefach/Velindre WwTW | 2264 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 233104 | 239913 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9JB | SA389JB | sa38 9jb | sa389jb | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 1644 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 231177 | 239234 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9JD | SA389JD | sa38 9jd | sa389jd | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 2772 | 1488 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.73 | 14.79 | 16.35 | 231758 | 237961 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9JE | SA389JE | sa38 9je | sa389je | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 3097 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 232295 | 236864 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9JF | SA389JF | sa38 9jf | sa389jf | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 3510 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 232671 | 237050 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9JG | SA389JG | sa38 9jg | sa389jg | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 2799 | 1365 | 1200to1500 | 2.73 | 2 | 1.47 | 25.44 | 13.57 | 15 | 232451 | 238811 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9JH | SA389JH | sa38 9jh | sa389jh | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 384 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230657 | 240465 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9JJ | SA389JJ | sa38 9jj | sa389jj | Ceredigion | Sir Ceredigion | Cenarth WwTW | 225 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 226476 | 241862 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9JL | SA389JL | sa38 9jl | sa389jl | Carmarthenshire | Sir Gaerfyrddin | Cenarth WwTW | 337 | 1138 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.21 | 11.31 | 12.5 | 226871 | 241494 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9JN | SA389JN | sa38 9jn | sa389jn | Carmarthenshire | Sir Gaerfyrddin | Cenarth WwTW | 556 | 1169 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.79 | 11.62 | 12.84 | 226112 | 241360 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9JP | SA389JP | sa38 9jp | sa389jp | Ceredigion | Sir Ceredigion | Cenarth WwTW | 160 | 1159 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.6 | 11.52 | 12.73 | 226695 | 241772 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9JQ | SA389JQ | sa38 9jq | sa389jq | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 1765 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 231786 | 239609 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9JR | SA389JR | sa38 9jr | sa389jr | Ceredigion | Sir Ceredigion | Cenarth WwTW | 117 | 1159 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.6 | 11.52 | 12.73 | 226613 | 241774 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9JS | SA389JS | sa38 9js | sa389js | Ceredigion | Sir Ceredigion | Cenarth WwTW | 416 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 226467 | 242063 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9JT | SA389JT | sa38 9jt | sa389jt | Ceredigion | Sir Ceredigion | Cenarth WwTW | 828 | 1159 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.6 | 11.52 | 12.73 | 226603 | 242490 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9JU | SA389JU | sa38 9ju | sa389ju | Ceredigion | Sir Ceredigion | Cenarth WwTW | 880 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 226072 | 242381 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9JW | SA389JW | sa38 9jw | sa389jw | Ceredigion | Sir Ceredigion | Cenarth WwTW | 96 | 1159 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.6 | 11.52 | 12.73 | 226664 | 241707 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9JX | SA389JX | sa38 9jx | sa389jx | Ceredigion | Sir Ceredigion | Abercych WwTW | 1829 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 225093 | 242878 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9JY | SA389JY | sa38 9jy | sa389jy | Ceredigion | Sir Ceredigion | Abercych WwTW | 2160 | 1096 | 900to1200 | 2.19 | 1.61 | 1.18 | 20.43 | 10.89 | 12.04 | 224577 | 243356 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9JZ | SA389JZ | sa38 9jz | sa389jz | Ceredigion | Sir Ceredigion | Cenarth WwTW | 295 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 226457 | 241931 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9LA | SA389LA | sa38 9la | sa389la | Ceredigion | Sir Ceredigion | Abercych WwTW | 604 | 1115 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.78 | 11.08 | 12.25 | 224713 | 241689 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9LB | SA389LB | sa38 9lb | sa389lb | Ceredigion | Sir Ceredigion | Cenarth WwTW | 1112 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 225516 | 241988 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9LD | SA389LD | sa38 9ld | sa389ld | Carmarthenshire | Sir Gaerfyrddin | Cenarth WwTW | 1563 | 1265 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.58 | 12.57 | 13.9 | 226536 | 240100 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LE | SA389LE | sa38 9le | sa389le | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 1768 | 1282 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.89 | 12.74 | 14.09 | 227903 | 240197 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LG | SA389LG | sa38 9lg | sa389lg | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 1712 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 227903 | 239475 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LJ | SA389LJ | sa38 9lj | sa389lj | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 472 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 228846 | 236127 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LL | SA389LL | sa38 9ll | sa389ll | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 407 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230553 | 240411 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LN | SA389LN | sa38 9ln | sa389ln | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 601 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 230625 | 240227 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LP | SA389LP | sa38 9lp | sa389lp | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 1424 | 1456 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.14 | 14.47 | 16 | 229775 | 238287 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LR | SA389LR | sa38 9lr | sa389lr | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 1229 | 1478 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.55 | 14.69 | 16.24 | 228988 | 237226 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LS | SA389LS | sa38 9ls | sa389ls | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 652 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 228827 | 236478 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LT | SA389LT | sa38 9lt | sa389lt | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 400 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 228955 | 236224 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LU | SA389LU | sa38 9lu | sa389lu | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 337 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 229261 | 236373 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LW | SA389LW | sa38 9lw | sa389lw | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 914 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 230403 | 239264 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LX | SA389LX | sa38 9lx | sa389lx | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 612 | 1574 | Over1500 | 3.15 | 2.31 | 1.69 | 29.34 | 15.65 | 17.29 | 229781 | 236431 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LY | SA389LY | sa38 9ly | sa389ly | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 511 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 229365 | 235532 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9LZ | SA389LZ | sa38 9lz | sa389lz | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 1127 | 1569 | Over1500 | 3.14 | 2.3 | 1.69 | 29.24 | 15.6 | 17.24 | 229460 | 234923 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9NA | SA389NA | sa38 9na | sa389na | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 866 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 228542 | 235639 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9NB | SA389NB | sa38 9nb | sa389nb | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 1261 | 1587 | Over1500 | 3.18 | 2.32 | 1.7 | 29.58 | 15.78 | 17.44 | 230510 | 235654 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9ND | SA389ND | sa38 9nd | sa389nd | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 2066 | 1587 | Over1500 | 3.18 | 2.32 | 1.7 | 29.58 | 15.78 | 17.44 | 231348 | 235703 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9NE | SA389NE | sa38 9ne | sa389ne | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 2109 | 1587 | Over1500 | 3.18 | 2.32 | 1.7 | 29.58 | 15.78 | 17.44 | 231354 | 235522 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9NG | SA389NG | sa38 9ng | sa389ng | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 3149 | 1808 | Over1500 | 3.62 | 2.65 | 1.94 | 33.7 | 17.97 | 19.86 | 232319 | 235111 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9NH | SA389NH | sa38 9nh | sa389nh | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 2611 | 1674 | Over1500 | 3.35 | 2.45 | 1.8 | 31.2 | 16.64 | 18.39 | 231024 | 234071 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9NJ | SA389NJ | sa38 9nj | sa389nj | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 2462 | 1674 | Over1500 | 3.35 | 2.45 | 1.8 | 31.2 | 16.64 | 18.39 | 230627 | 233960 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9NL | SA389NL | sa38 9nl | sa389nl | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 3466 | 1828 | Over1500 | 3.66 | 2.68 | 1.96 | 34.07 | 18.17 | 20.08 | 231826 | 233656 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9NN | SA389NN | sa38 9nn | sa389nn | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 3359 | 1865 | Over1500 | 3.73 | 2.73 | 2 | 34.76 | 18.54 | 20.49 | 232589 | 235310 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9NP | SA389NP | sa38 9np | sa389np | Ceredigion | Sir Ceredigion | Adpar WwTW | 581 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230507 | 241395 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9NQ | SA389NQ | sa38 9nq | sa389nq | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 2622 | 1645 | Over1500 | 3.29 | 2.41 | 1.77 | 30.66 | 16.35 | 18.07 | 231487 | 234579 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9NR | SA389NR | sa38 9nr | sa389nr | Ceredigion | Sir Ceredigion | Adpar WwTW | 449 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 230493 | 241263 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9NS | SA389NS | sa38 9ns | sa389ns | Ceredigion | Sir Ceredigion | Adpar WwTW | 335 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230779 | 240993 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9NT | SA389NT | sa38 9nt | sa389nt | Ceredigion | Sir Ceredigion | Adpar WwTW | 628 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 230424 | 241438 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9NW | SA389NW | sa38 9nw | sa389nw | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 1796 | 1587 | Over1500 | 3.18 | 2.32 | 1.7 | 29.58 | 15.78 | 17.44 | 230844 | 236974 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9NX | SA389NX | sa38 9nx | sa389nx | Ceredigion | Sir Ceredigion | Adpar WwTW | 408 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230580 | 241213 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9NY | SA389NY | sa38 9ny | sa389ny | Ceredigion | Sir Ceredigion | Adpar WwTW | 1386 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 229700 | 241948 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9NZ | SA389NZ | sa38 9nz | sa389nz | Ceredigion | Sir Ceredigion | Adpar WwTW | 1605 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 229409 | 241995 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PA | SA389PA | sa38 9pa | sa389pa | Ceredigion | Sir Ceredigion | Adpar WwTW | 1682 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 230128 | 242455 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PB | SA389PB | sa38 9pb | sa389pb | Ceredigion | Sir Ceredigion | Adpar WwTW | 1628 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 229288 | 241905 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PD | SA389PD | sa38 9pd | sa389pd | Ceredigion | Sir Ceredigion | Adpar WwTW | 1722 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 229296 | 242049 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PE | SA389PE | sa38 9pe | sa389pe | Ceredigion | Sir Ceredigion | Adpar WwTW | 2292 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 228813 | 242370 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PF | SA389PF | sa38 9pf | sa389pf | Ceredigion | Sir Ceredigion | Cenarth WwTW | 1995 | 1166 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.73 | 11.59 | 12.81 | 227645 | 243348 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PG | SA389PG | sa38 9pg | sa389pg | Ceredigion | Sir Ceredigion | Cenarth WwTW | 1165 | 1180 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.99 | 11.73 | 12.96 | 226619 | 242826 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PH | SA389PH | sa38 9ph | sa389ph | Ceredigion | Sir Ceredigion | Cenarth WwTW | 1188 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 227699 | 242058 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PJ | SA389PJ | sa38 9pj | sa389pj | Ceredigion | Sir Ceredigion | Beulah WwTW | 1281 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 229938 | 244964 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PL | SA389PL | sa38 9pl | sa389pl | Ceredigion | Sir Ceredigion | Beulah WwTW | 1786 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 230421 | 244642 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PN | SA389PN | sa38 9pn | sa389pn | Ceredigion | Sir Ceredigion | Adpar WwTW | 2268 | 1211 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.57 | 12.04 | 13.31 | 231013 | 243022 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PP | SA389PP | sa38 9pp | sa389pp | Ceredigion | Sir Ceredigion | Beulah WwTW | 2250 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 230363 | 244091 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PQ | SA389PQ | sa38 9pq | sa389pq | Ceredigion | Sir Ceredigion | Cenarth WwTW | 1665 | 1180 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.99 | 11.73 | 12.96 | 227303 | 243161 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PR | SA389PR | sa38 9pr | sa389pr | Ceredigion | Sir Ceredigion | Beulah WwTW | 2717 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 228682 | 243563 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PS | SA389PS | sa38 9ps | sa389ps | Ceredigion | Sir Ceredigion | Adpar WwTW | 459 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230717 | 241216 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PX | SA389PX | sa38 9px | sa389px | Ceredigion | Sir Ceredigion | Adpar WwTW | 743 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 230722 | 241522 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PY | SA389PY | sa38 9py | sa389py | Ceredigion | Sir Ceredigion | Adpar WwTW | 2567 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 229508 | 243183 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9PZ | SA389PZ | sa38 9pz | sa389pz | Ceredigion | Sir Ceredigion | Beulah WwTW | 2376 | 1233 | 1200to1500 | 2.47 | 1.81 | 1.32 | 22.98 | 12.26 | 13.55 | 229820 | 243809 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QA | SA389QA | sa38 9qa | sa389qa | Ceredigion | Sir Ceredigion | Beulah WwTW | 730 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 229646 | 245449 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QB | SA389QB | sa38 9qb | sa389qb | Ceredigion | Sir Ceredigion | Beulah WwTW | 650 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 228833 | 246097 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QD | SA389QD | sa38 9qd | sa389qd | Ceredigion | Sir Ceredigion | Beulah WwTW | 1041 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 228811 | 245363 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QE | SA389QE | sa38 9qe | sa389qe | Ceredigion | Sir Ceredigion | Beulah WwTW | 687 | 1222 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.78 | 12.15 | 13.43 | 228889 | 246511 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QF | SA389QF | sa38 9qf | sa389qf | Ceredigion | Sir Ceredigion | Beulah WwTW | 454 | 1199 | 900to1200 | 2.4 | 1.76 | 1.29 | 22.35 | 11.92 | 13.17 | 229088 | 246389 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QG | SA389QG | sa38 9qg | sa389qg | Ceredigion | Sir Ceredigion | Beulah WwTW | 401 | 1170 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.81 | 11.63 | 12.85 | 229881 | 246151 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QH | SA389QH | sa38 9qh | sa389qh | Ceredigion | Sir Ceredigion | Beulah WwTW | 1520 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 230953 | 246535 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QJ | SA389QJ | sa38 9qj | sa389qj | Ceredigion | Sir Ceredigion | Beulah WwTW | 1344 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 230373 | 247165 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QL | SA389QL | sa38 9ql | sa389ql | Ceredigion | Sir Ceredigion | Beulah WwTW | 1682 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 230084 | 247730 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QN | SA389QN | sa38 9qn | sa389qn | Ceredigion | Sir Ceredigion | Beulah WwTW | 1501 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 229095 | 247611 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QP | SA389QP | sa38 9qp | sa389qp | Ceredigion | Sir Ceredigion | Beulah WwTW | 1278 | 1232 | 1200to1500 | 2.47 | 1.8 | 1.32 | 22.96 | 12.25 | 13.54 | 228285 | 245708 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QQ | SA389QQ | sa38 9qq | sa389qq | Ceredigion | Sir Ceredigion | Beulah WwTW | 1431 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 230727 | 245458 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QR | SA389QR | sa38 9qr | sa389qr | Ceredigion | Sir Ceredigion | Beulah WwTW | 1514 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 228481 | 245023 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QS | SA389QS | sa38 9qs | sa389qs | Ceredigion | Sir Ceredigion | Beulah WwTW | 2568 | 1195 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.27 | 11.88 | 13.13 | 227646 | 244363 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QT | SA389QT | sa38 9qt | sa389qt | Ceredigion | Sir Ceredigion | Beulah WwTW | 1293 | 1232 | 1200to1500 | 2.47 | 1.8 | 1.32 | 22.96 | 12.25 | 13.54 | 228194 | 246030 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QU | SA389QU | sa38 9qu | sa389qu | Ceredigion | Sir Ceredigion | Beulah WwTW | 2534 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 227044 | 246858 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QW | SA389QW | sa38 9qw | sa389qw | Ceredigion | Sir Ceredigion | Adpar WwTW | 651 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230944 | 241286 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9QY | SA389QY | sa38 9qy | sa389qy | Ceredigion | Sir Ceredigion | Adpar WwTW | 608 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 230903 | 241266 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA38 9RA | SA389RA | sa38 9ra | sa389ra | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 681 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 229879 | 241102 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RB | SA389RB | sa38 9rb | sa389rb | Carmarthenshire | Sir Gaerfyrddin | Cenarth WwTW | 1455 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 227849 | 240952 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RD | SA389RD | sa38 9rd | sa389rd | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 655 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 229868 | 241000 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RE | SA389RE | sa38 9re | sa389re | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 746 | 1263 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.54 | 12.55 | 13.88 | 229385 | 240414 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RF | SA389RF | sa38 9rf | sa389rf | Carmarthenshire | Sir Gaerfyrddin | Adpar WwTW | 481 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 230137 | 240494 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RG | SA389RG | sa38 9rg | sa389rg | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 102 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 229702 | 239708 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RH | SA389RH | sa38 9rh | sa389rh | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 23 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 229599 | 239677 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RJ | SA389RJ | sa38 9rj | sa389rj | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 940 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 228993 | 238982 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RL | SA389RL | sa38 9rl | sa389rl | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 2184 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 227539 | 238978 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RN | SA389RN | sa38 9rn | sa389rn | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 2261 | 1367 | 1200to1500 | 2.74 | 2 | 1.47 | 25.48 | 13.59 | 15.02 | 227691 | 238488 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RP | SA389RP | sa38 9rp | sa389rp | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 1663 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 227977 | 237035 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RR | SA389RR | sa38 9rr | sa389rr | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 1728 | 1446 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.95 | 14.37 | 15.89 | 227584 | 236118 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RS | SA389RS | sa38 9rs | sa389rs | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 2036 | 1367 | 1200to1500 | 2.74 | 2 | 1.47 | 25.48 | 13.59 | 15.02 | 228439 | 238027 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RT | SA389RT | sa38 9rt | sa389rt | Carmarthenshire | Sir Gaerfyrddin | Danrhelyg STW | 545 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 229904 | 239248 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA38 9RW | SA389RW | sa38 9rw | sa389rw | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 2368 | 1367 | 1200to1500 | 2.74 | 2 | 1.47 | 25.48 | 13.59 | 15.02 | 227543 | 237616 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AA | SA399AA | sa39 9aa | sa399aa | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 107 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244670 | 236419 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AB | SA399AB | sa39 9ab | sa399ab | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 325 | 1519 | Over1500 | 3.04 | 2.22 | 1.63 | 28.31 | 15.1 | 16.69 | 244925 | 236516 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AD | SA399AD | sa39 9ad | sa399ad | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 178 | 1519 | Over1500 | 3.04 | 2.22 | 1.63 | 28.31 | 15.1 | 16.69 | 244683 | 236658 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AE | SA399AE | sa39 9ae | sa399ae | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 1180 | 1456 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.14 | 14.47 | 16 | 244619 | 237680 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AF | SA399AF | sa39 9af | sa399af | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 257 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244582 | 236244 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AG | SA399AG | sa39 9ag | sa399ag | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 1649 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 243804 | 237944 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AH | SA399AH | sa39 9ah | sa399ah | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 2151 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 242768 | 237626 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AJ | SA399AJ | sa39 9aj | sa399aj | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 2108 | 1521 | Over1500 | 3.04 | 2.23 | 1.63 | 28.35 | 15.12 | 16.71 | 242509 | 236762 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AL | SA399AL | sa39 9al | sa399al | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 903 | 1553 | Over1500 | 3.11 | 2.27 | 1.67 | 28.95 | 15.44 | 17.06 | 243718 | 236694 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AN | SA399AN | sa39 9an | sa399an | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 375 | 1553 | Over1500 | 3.11 | 2.27 | 1.67 | 28.95 | 15.44 | 17.06 | 244226 | 236524 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AP | SA399AP | sa39 9ap | sa399ap | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 317 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244584 | 236183 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AR | SA399AR | sa39 9ar | sa399ar | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 418 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244743 | 236107 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AS | SA399AS | sa39 9as | sa399as | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 983 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 245417 | 235954 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AT | SA399AT | sa39 9at | sa399at | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 1864 | 1640 | Over1500 | 3.28 | 2.4 | 1.76 | 30.57 | 16.3 | 18.02 | 246252 | 235636 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AU | SA399AU | sa39 9au | sa399au | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 1964 | 1688 | Over1500 | 3.38 | 2.47 | 1.81 | 31.46 | 16.78 | 18.55 | 246253 | 235439 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AW | SA399AW | sa39 9aw | sa399aw | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 2547 | 1555 | Over1500 | 3.11 | 2.28 | 1.67 | 28.98 | 15.46 | 17.08 | 247136 | 236730 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AX | SA399AX | sa39 9ax | sa399ax | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 1979 | 1640 | Over1500 | 3.28 | 2.4 | 1.76 | 30.57 | 16.3 | 18.02 | 246429 | 235745 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AY | SA399AY | sa39 9ay | sa399ay | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 2491 | 1555 | Over1500 | 3.11 | 2.28 | 1.67 | 28.98 | 15.46 | 17.08 | 247089 | 236590 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9AZ | SA399AZ | sa39 9az | sa399az | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 2827 | 1555 | Over1500 | 3.11 | 2.28 | 1.67 | 28.98 | 15.46 | 17.08 | 247406 | 236839 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BA | SA399BA | sa39 9ba | sa399ba | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 2436 | 1555 | Over1500 | 3.11 | 2.28 | 1.67 | 28.98 | 15.46 | 17.08 | 247002 | 236902 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BB | SA399BB | sa39 9bb | sa399bb | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 1398 | 1577 | Over1500 | 3.16 | 2.31 | 1.69 | 29.39 | 15.68 | 17.33 | 245781 | 237247 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BD | SA399BD | sa39 9bd | sa399bd | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 1004 | 1519 | Over1500 | 3.04 | 2.22 | 1.63 | 28.31 | 15.1 | 16.69 | 245412 | 237091 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BE | SA399BE | sa39 9be | sa399be | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 3026 | 1543 | Over1500 | 3.09 | 2.26 | 1.66 | 28.76 | 15.34 | 16.95 | 247804 | 237516 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BG | SA399BG | sa39 9bg | sa399bg | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 2168 | 1543 | Over1500 | 3.09 | 2.26 | 1.66 | 28.76 | 15.34 | 16.95 | 247989 | 238402 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BH | SA399BH | sa39 9bh | sa399bh | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 3244 | 1661 | Over1500 | 3.32 | 2.43 | 1.78 | 30.96 | 16.51 | 18.25 | 247787 | 235898 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BJ | SA399BJ | sa39 9bj | sa399bj | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 3076 | 1661 | Over1500 | 3.32 | 2.43 | 1.78 | 30.96 | 16.51 | 18.25 | 247529 | 235560 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BL | SA399BL | sa39 9bl | sa399bl | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 2898 | 1712 | Over1500 | 3.43 | 2.51 | 1.84 | 31.91 | 17.02 | 18.81 | 247023 | 234911 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BP | SA399BP | sa39 9bp | sa399bp | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 394 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 244474 | 236127 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BQ | SA399BQ | sa39 9bq | sa399bq | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 2086 | 1610 | Over1500 | 3.22 | 2.36 | 1.73 | 30.01 | 16 | 17.69 | 246594 | 235888 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BS | SA399BS | sa39 9bs | sa399bs | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 318 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 244391 | 236260 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BT | SA399BT | sa39 9bt | sa399bt | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 358 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 244319 | 236279 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BU | SA399BU | sa39 9bu | sa399bu | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 343 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 244300 | 236334 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BX | SA399BX | sa39 9bx | sa399bx | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 1559 | 1663 | Over1500 | 3.33 | 2.44 | 1.79 | 31 | 16.53 | 18.27 | 244063 | 235037 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9BY | SA399BY | sa39 9by | sa399by | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 2741 | 1814 | Over1500 | 3.63 | 2.66 | 1.95 | 33.81 | 18.03 | 19.93 | 242998 | 234276 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DA | SA399DA | sa39 9da | sa399da | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 2482 | 1802 | Over1500 | 3.61 | 2.64 | 1.94 | 33.59 | 17.91 | 19.8 | 243002 | 233415 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DD | SA399DD | sa39 9dd | sa399dd | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 2897 | 1663 | Over1500 | 3.33 | 2.44 | 1.79 | 31 | 16.53 | 18.27 | 241814 | 235705 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DG | SA399DG | sa39 9dg | sa399dg | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1592 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 248035 | 241284 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DH | SA399DH | sa39 9dh | sa399dh | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 890 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 248416 | 239779 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DJ | SA399DJ | sa39 9dj | sa399dj | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1521 | 1361 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.37 | 13.53 | 14.95 | 248491 | 241546 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DL | SA399DL | sa39 9dl | sa399dl | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 2053 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 249083 | 242249 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DN | SA399DN | sa39 9dn | sa399dn | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1483 | 1442 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.88 | 14.33 | 15.84 | 249736 | 241583 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DP | SA399DP | sa39 9dp | sa399dp | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 437 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 249358 | 240607 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DQ | SA399DQ | sa39 9dq | sa399dq | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 441 | 1445 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.93 | 14.36 | 15.88 | 248793 | 240370 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DR | SA399DR | sa39 9dr | sa399dr | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 309 | 1445 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.93 | 14.36 | 15.88 | 249494 | 240294 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DS | SA399DS | sa39 9ds | sa399ds | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 468 | 1495 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.86 | 14.86 | 16.43 | 249602 | 239961 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DT | SA399DT | sa39 9dt | sa399dt | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 259 | 1445 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.93 | 14.36 | 15.88 | 249456 | 240160 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DU | SA399DU | sa39 9du | sa399du | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 371 | 1445 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.93 | 14.36 | 15.88 | 249146 | 239833 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DW | SA399DW | sa39 9dw | sa399dw | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1089 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 249378 | 241274 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DX | SA399DX | sa39 9dx | sa399dx | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1076 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 248690 | 239253 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DY | SA399DY | sa39 9dy | sa399dy | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1257 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 248576 | 239109 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DZ | SA399DZ | sa39 9dz | sa399dz | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1790 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 248030 | 238846 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9EA | SA399EA | sa39 9ea | sa399ea | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1410 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 248519 | 238966 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9EB | SA399EB | sa39 9eb | sa399eb | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1459 | 1631 | Over1500 | 3.26 | 2.39 | 1.75 | 30.4 | 16.21 | 17.92 | 250066 | 239026 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9EE | SA399EE | sa39 9ee | sa399ee | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1582 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 249499 | 238647 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9EF | SA399EF | sa39 9ef | sa399ef | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1232 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 248565 | 239144 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9EG | SA399EG | sa39 9eg | sa399eg | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 3691 | 1695 | Over1500 | 3.39 | 2.48 | 1.82 | 31.59 | 16.85 | 18.62 | 249425 | 236516 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9EH | SA399EH | sa39 9eh | sa399eh | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 4431 | 1813 | Over1500 | 3.63 | 2.66 | 1.95 | 33.79 | 18.02 | 19.92 | 249222 | 235770 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9EL | SA399EL | sa39 9el | sa399el | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 4315 | 1849 | Over1500 | 3.7 | 2.71 | 1.99 | 34.46 | 18.38 | 20.31 | 248705 | 235173 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9ER | SA399ER | sa39 9er | sa399er | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 427 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244592 | 236073 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9ES | SA399ES | sa39 9es | sa399es | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 492 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244539 | 236012 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9ET | SA399ET | sa39 9et | sa399et | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 511 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244719 | 236003 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9EU | SA399EU | sa39 9eu | sa399eu | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 592 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244764 | 235931 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9EX | SA399EX | sa39 9ex | sa399ex | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 724 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 245052 | 235935 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HA | SA399HA | sa39 9ha | sa399ha | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 591 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244569 | 235910 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HB | SA399HB | sa39 9hb | sa399hb | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 747 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244538 | 235756 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HD | SA399HD | sa39 9hd | sa399hd | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 798 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 244226 | 235795 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HE | SA399HE | sa39 9he | sa399he | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 917 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244531 | 235586 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HF | SA399HF | sa39 9hf | sa399hf | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 659 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 244485 | 235851 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HG | SA399HG | sa39 9hg | sa399hg | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 787 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244510 | 235718 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HH | SA399HH | sa39 9hh | sa399hh | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 931 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244708 | 235575 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HL | SA399HL | sa39 9hl | sa399hl | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 1681 | 1621 | Over1500 | 3.24 | 2.37 | 1.74 | 30.21 | 16.11 | 17.81 | 244625 | 234819 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HN | SA399HN | sa39 9hn | sa399hn | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 2206 | 1700 | Over1500 | 3.4 | 2.49 | 1.83 | 31.69 | 16.9 | 18.68 | 244392 | 233504 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HP | SA399HP | sa39 9hp | sa399hp | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 2396 | 1691 | Over1500 | 3.38 | 2.48 | 1.82 | 31.52 | 16.81 | 18.58 | 245580 | 234314 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HQ | SA399HQ | sa39 9hq | sa399hq | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 831 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244665 | 235672 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HR | SA399HR | sa39 9hr | sa399hr | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 884 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244558 | 235617 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HS | SA399HS | sa39 9hs | sa399hs | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 1430 | 1621 | Over1500 | 3.24 | 2.37 | 1.74 | 30.21 | 16.11 | 17.81 | 244559 | 235071 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HT | SA399HT | sa39 9ht | sa399ht | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 493 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 245676 | 239663 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HU | SA399HU | sa39 9hu | sa399hu | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 699 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 245509 | 239421 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HW | SA399HW | sa39 9hw | sa399hw | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 604 | 1609 | Over1500 | 3.22 | 2.36 | 1.73 | 29.99 | 15.99 | 17.68 | 244509 | 235903 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HX | SA399HX | sa39 9hx | sa399hx | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 826 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 245340 | 239308 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HY | SA399HY | sa39 9hy | sa399hy | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 391 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 245637 | 239758 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9HZ | SA399HZ | sa39 9hz | sa399hz | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 869 | 1434 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.73 | 14.25 | 15.76 | 244677 | 239812 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9JA | SA399JA | sa39 9ja | sa399ja | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 271 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 245695 | 239943 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9JB | SA399JB | sa39 9jb | sa399jb | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 326 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 245607 | 240424 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9JD | SA399JD | sa39 9jd | sa399jd | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 993 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 244599 | 240559 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9JE | SA399JE | sa39 9je | sa399je | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 1494 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 244920 | 241501 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9JH | SA399JH | sa39 9jh | sa399jh | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 608 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 245649 | 239533 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9JJ | SA399JJ | sa39 9jj | sa399jj | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 1047 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 246065 | 239245 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9JL | SA399JL | sa39 9jl | sa399jl | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 1413 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 245845 | 238752 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9JN | SA399JN | sa39 9jn | sa399jn | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 2192 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 246576 | 238216 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9JP | SA399JP | sa39 9jp | sa399jp | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 2074 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 247684 | 238785 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9JR | SA399JR | sa39 9jr | sa399jr | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 1147 | 1393 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.96 | 13.85 | 15.3 | 246570 | 239735 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9JU | SA399JU | sa39 9ju | sa399ju | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 910 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 245391 | 239215 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9JX | SA399JX | sa39 9jx | sa399jx | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 1176 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 245259 | 238967 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9JY | SA399JY | sa39 9jy | sa399jy | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 1865 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 244196 | 238321 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9JZ | SA399JZ | sa39 9jz | sa399jz | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 1806 | 1447 | 1200to1500 | 2.9 | 2.12 | 1.55 | 26.97 | 14.38 | 15.9 | 243227 | 239054 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9LA | SA399LA | sa39 9la | sa399la | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 1326 | 1385 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.81 | 13.77 | 15.22 | 243019 | 239564 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9LB | SA399LB | sa39 9lb | sa399lb | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 1622 | 1491 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.79 | 14.82 | 16.38 | 244023 | 239428 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9LD | SA399LD | sa39 9ld | sa399ld | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 960 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 244956 | 239322 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9LG | SA399LG | sa39 9lg | sa399lg | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1626 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 247874 | 241141 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9LH | SA399LH | sa39 9lh | sa399lh | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1474 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 247755 | 240490 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9LJ | SA399LJ | sa39 9lj | sa399lj | Carmarthenshire | Sir Gaerfyrddin | Llanfihangel-Ar-Arth STW | 1807 | 1393 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.96 | 13.85 | 15.3 | 247291 | 240268 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9LL | SA399LL | sa39 9ll | sa399ll | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1946 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 247346 | 240792 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9LN | SA399LN | sa39 9ln | sa399ln | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 2379 | 1395 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26 | 13.87 | 15.33 | 247147 | 241827 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9LP | SA399LP | sa39 9lp | sa399lp | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 3073 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 247196 | 242675 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9LT | SA399LT | sa39 9lt | sa399lt | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 2086 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 247183 | 241338 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9LU | SA399LU | sa39 9lu | sa399lu | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 1632 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 246573 | 241341 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9LW | SA399LW | sa39 9lw | sa399lw | Ceredigion | Sir Ceredigion | Bryndulais STW | 1997 | 1361 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.37 | 13.53 | 14.95 | 248082 | 241855 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9LX | SA399LX | sa39 9lx | sa399lx | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 1139 | 1414 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.35 | 14.06 | 15.54 | 246099 | 241082 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9LY | SA399LY | sa39 9ly | sa399ly | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 893 | 1414 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.35 | 14.06 | 15.54 | 245654 | 240998 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9LZ | SA399LZ | sa39 9lz | sa399lz | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 1252 | 1414 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.35 | 14.06 | 15.54 | 245635 | 241363 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9NA | SA399NA | sa39 9na | sa399na | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 1595 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 245486 | 241715 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9NB | SA399NB | sa39 9nb | sa399nb | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 2411 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 245839 | 242505 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA39 9TU | SA399TU | sa39 9tu | sa399tu | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 189 | 1445 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.93 | 14.36 | 15.88 | 249370 | 240118 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9AA | SA409AA | sa40 9aa | sa409aa | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1132 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 252801 | 243614 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9AB | SA409AB | sa40 9ab | sa409ab | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1106 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 252801 | 243517 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QA | SA409QA | sa40 9qa | sa409qa | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1051 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252291 | 244150 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QB | SA409QB | sa40 9qb | sa409qb | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1097 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252273 | 244215 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QD | SA409QD | sa40 9qd | sa409qd | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1174 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252345 | 244261 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QE | SA409QE | sa40 9qe | sa409qe | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1822 | 1365 | 1200to1500 | 2.73 | 2 | 1.47 | 25.44 | 13.57 | 15 | 253005 | 244560 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QG | SA409QG | sa40 9qg | sa409qg | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 2492 | 1365 | 1200to1500 | 2.73 | 2 | 1.47 | 25.44 | 13.57 | 15 | 253435 | 245077 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QJ | SA409QJ | sa40 9qj | sa409qj | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 2833 | 1413 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.34 | 14.05 | 15.52 | 253591 | 245395 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QL | SA409QL | sa40 9ql | sa409ql | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 3315 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 254075 | 245602 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QN | SA409QN | sa40 9qn | sa409qn | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 3006 | 1389 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.89 | 13.81 | 15.26 | 255040 | 245816 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QP | SA409QP | sa40 9qp | sa409qp | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 3313 | 1430 | 1200to1500 | 2.86 | 2.09 | 1.54 | 26.65 | 14.21 | 15.71 | 254591 | 244924 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QQ | SA409QQ | sa40 9qq | sa409qq | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 2835 | 1413 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.34 | 14.05 | 15.52 | 253660 | 245336 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QR | SA409QR | sa40 9qr | sa409qr | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 3139 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 254779 | 243984 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QS | SA409QS | sa40 9qs | sa409qs | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 2100 | 1420 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.47 | 14.12 | 15.6 | 253779 | 243697 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QT | SA409QT | sa40 9qt | sa409qt | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1926 | 1420 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.47 | 14.12 | 15.6 | 253621 | 243597 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QU | SA409QU | sa40 9qu | sa409qu | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1850 | 1420 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.47 | 14.12 | 15.6 | 253544 | 243594 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QX | SA409QX | sa40 9qx | sa409qx | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1912 | 1420 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.47 | 14.12 | 15.6 | 253613 | 243559 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9QZ | SA409QZ | sa40 9qz | sa409qz | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 2068 | 1492 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.81 | 14.83 | 16.39 | 253674 | 242577 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RA | SA409RA | sa40 9ra | sa409ra | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1258 | 1457 | 1200to1500 | 2.92 | 2.13 | 1.56 | 27.16 | 14.48 | 16.01 | 252982 | 243279 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RB | SA409RB | sa40 9rb | sa409rb | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 2845 | 1501 | Over1500 | 3 | 2.2 | 1.61 | 27.98 | 14.92 | 16.49 | 254530 | 242795 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RD | SA409RD | sa40 9rd | sa409rd | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 2680 | 1495 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.86 | 14.86 | 16.43 | 254283 | 242471 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RE | SA409RE | sa40 9re | sa409re | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 3617 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 255074 | 241903 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RF | SA409RF | sa40 9rf | sa409rf | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 3386 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 255493 | 241684 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RG | SA409RG | sa40 9rg | sa409rg | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1094 | 1457 | 1200to1500 | 2.92 | 2.13 | 1.56 | 27.16 | 14.48 | 16.01 | 252804 | 243441 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RL | SA409RL | sa40 9rl | sa409rl | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1036 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252404 | 244046 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RN | SA409RN | sa40 9rn | sa409rn | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1182 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 252768 | 243819 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RP | SA409RP | sa40 9rp | sa409rp | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1420 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 253051 | 243769 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RQ | SA409RQ | sa40 9rq | sa409rq | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1298 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 252896 | 243822 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RR | SA409RR | sa40 9rr | sa409rr | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1654 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 253326 | 243677 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RS | SA409RS | sa40 9rs | sa409rs | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 687 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252238 | 243720 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RT | SA409RT | sa40 9rt | sa409rt | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 992 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 252585 | 243758 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RU | SA409RU | sa40 9ru | sa409ru | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 931 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 252547 | 243700 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RX | SA409RX | sa40 9rx | sa409rx | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 816 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252366 | 243769 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9RZ | SA409RZ | sa40 9rz | sa409rz | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 682 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252208 | 243746 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9SA | SA409SA | sa40 9sa | sa409sa | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 515 | 1410 | 1200to1500 | 2.82 | 2.07 | 1.51 | 26.28 | 14.02 | 15.49 | 252191 | 243047 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9SB | SA409SB | sa40 9sb | sa409sb | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1958 | 1548 | Over1500 | 3.1 | 2.27 | 1.66 | 28.85 | 15.39 | 17.01 | 252115 | 241347 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9SD | SA409SD | sa40 9sd | sa409sd | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 248 | 1410 | 1200to1500 | 2.82 | 2.07 | 1.51 | 26.28 | 14.02 | 15.49 | 251971 | 243289 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9SE | SA409SE | sa40 9se | sa409se | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 624 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 251238 | 242873 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9SF | SA409SF | sa40 9sf | sa409sf | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1003 | 1407 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.22 | 13.99 | 15.46 | 252654 | 243640 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9SG | SA409SG | sa40 9sg | sa409sg | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 1903 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 251093 | 241470 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9SH | SA409SH | sa40 9sh | sa409sh | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 637 | 1495 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.86 | 14.86 | 16.43 | 249783 | 240457 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9SJ | SA409SJ | sa40 9sj | sa409sj | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1971 | 1545 | Over1500 | 3.09 | 2.26 | 1.66 | 28.8 | 15.36 | 16.97 | 251167 | 240316 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9SP | SA409SP | sa40 9sp | sa409sp | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 1377 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 252005 | 244613 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9SQ | SA409SQ | sa40 9sq | sa409sq | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 1352 | 1450 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.03 | 14.41 | 15.93 | 250301 | 240984 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9SR | SA409SR | sa40 9sr | sa409sr | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 1836 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 252001 | 245080 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9SS | SA409SS | sa40 9ss | sa409ss | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 1877 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 252068 | 245110 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9ST | SA409ST | sa40 9st | sa409st | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 2396 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 252294 | 245592 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9SU | SA409SU | sa40 9su | sa409su | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 2423 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 251591 | 245684 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9SX | SA409SX | sa40 9sx | sa409sx | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1615 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 250540 | 245908 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9SY | SA409SY | sa40 9sy | sa409sy | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1282 | 1270 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.67 | 12.62 | 13.95 | 250149 | 246025 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TA | SA409TA | sa40 9ta | sa409ta | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1069 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 250478 | 246808 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TB | SA409TB | sa40 9tb | sa409tb | Ceredigion | Sir Ceredigion | Gorsgoch STW | 2083 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 249427 | 249701 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TD | SA409TD | sa40 9td | sa409td | Ceredigion | Sir Ceredigion | Gorsgoch STW | 1038 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 248560 | 250305 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TE | SA409TE | sa40 9te | sa409te | Ceredigion | Sir Ceredigion | Gorsgoch STW | 795 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 248380 | 250548 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TF | SA409TF | sa40 9tf | sa409tf | Ceredigion | Sir Ceredigion | Gorsgoch STW | 331 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 247906 | 250574 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TG | SA409TG | sa40 9tg | sa409tg | Ceredigion | Sir Ceredigion | Gorsgoch STW | 568 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 248165 | 250644 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TH | SA409TH | sa40 9th | sa409th | Ceredigion | Sir Ceredigion | Gorsgoch STW | 2001 | 1410 | 1200to1500 | 2.82 | 2.07 | 1.51 | 26.28 | 14.02 | 15.49 | 245600 | 250741 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TJ | SA409TJ | sa40 9tj | sa409tj | Ceredigion | Sir Ceredigion | Gorsgoch STW | 1273 | 1410 | 1200to1500 | 2.82 | 2.07 | 1.51 | 26.28 | 14.02 | 15.49 | 246418 | 251172 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TL | SA409TL | sa40 9tl | sa409tl | Ceredigion | Sir Ceredigion | Gorsgoch STW | 1116 | 1389 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.89 | 13.81 | 15.26 | 247743 | 251807 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TN | SA409TN | sa40 9tn | sa409tn | Ceredigion | Sir Ceredigion | Gorsgoch STW | 780 | 1401 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.11 | 13.93 | 15.39 | 247251 | 251397 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TP | SA409TP | sa40 9tp | sa409tp | Ceredigion | Sir Ceredigion | Gorsgoch STW | 1341 | 1345 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.07 | 13.37 | 14.78 | 248940 | 250650 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TR | SA409TR | sa40 9tr | sa409tr | Ceredigion | Sir Ceredigion | Gorsgoch STW | 1445 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 248626 | 249683 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9TX | SA409TX | sa40 9tx | sa409tx | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 797 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252166 | 243928 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9TY | SA409TY | sa40 9ty | sa409ty | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 595 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252165 | 243664 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9TZ | SA409TZ | sa40 9tz | sa409tz | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 675 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252312 | 243596 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9UA | SA409UA | sa40 9ua | sa409ua | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 511 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252057 | 243653 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9UB | SA409UB | sa40 9ub | sa409ub | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 603 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252083 | 243749 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9UD | SA409UD | sa40 9ud | sa409ud | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 694 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 251916 | 243932 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9UE | SA409UE | sa40 9ue | sa409ue | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 781 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 251986 | 244001 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9UG | SA409UG | sa40 9ug | sa409ug | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 971 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 251767 | 244235 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9UH | SA409UH | sa40 9uh | sa409uh | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 981 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 251320 | 244159 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9UJ | SA409UJ | sa40 9uj | sa409uj | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 880 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 251060 | 243842 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9UL | SA409UL | sa40 9ul | sa409ul | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 1447 | 1361 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.37 | 13.53 | 14.95 | 250289 | 243448 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9UP | SA409UP | sa40 9up | sa409up | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 1815 | 1279 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.84 | 12.71 | 14.05 | 250187 | 244230 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9UR | SA409UR | sa40 9ur | sa409ur | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 2171 | 1267 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.61 | 12.59 | 13.92 | 250321 | 245112 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9UT | SA409UT | sa40 9ut | sa409ut | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1510 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 249334 | 245595 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9UU | SA409UU | sa40 9uu | sa409uu | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1781 | 1281 | 1200to1500 | 2.56 | 1.88 | 1.38 | 23.88 | 12.73 | 14.07 | 249427 | 245319 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9UX | SA409UX | sa40 9ux | sa409ux | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3157 | 1267 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.61 | 12.59 | 13.92 | 248594 | 244062 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9UY | SA409UY | sa40 9uy | sa409uy | Ceredigion | Sir Ceredigion | Bryndulais STW | 3443 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 247638 | 243268 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9UZ | SA409UZ | sa40 9uz | sa409uz | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1525 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 249250 | 245588 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9XA | SA409XA | sa40 9xa | sa409xa | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 2686 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 249039 | 243320 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9XB | SA409XB | sa40 9xb | sa409xb | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 2214 | 1361 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.37 | 13.53 | 14.95 | 249515 | 243116 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9XD | SA409XD | sa40 9xd | sa409xd | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 3629 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 246922 | 243454 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9XE | SA409XE | sa40 9xe | sa409xe | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3278 | 1331 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.81 | 13.23 | 14.62 | 247512 | 244457 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9XG | SA409XG | sa40 9xg | sa409xg | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 2481 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 247819 | 245231 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9XH | SA409XH | sa40 9xh | sa409xh | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 2031 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 247666 | 246130 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9XJ | SA409XJ | sa40 9xj | sa409xj | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 2136 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 247492 | 246248 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9XL | SA409XL | sa40 9xl | sa409xl | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1608 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 248179 | 246116 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9XP | SA409XP | sa40 9xp | sa409xp | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 911 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252186 | 244050 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9XS | SA409XS | sa40 9xs | sa409xs | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 850 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252115 | 244020 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9XT | SA409XT | sa40 9xt | sa409xt | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 829 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252056 | 244024 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9XX | SA409XX | sa40 9xx | sa409xx | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 972 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 252106 | 244159 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9XY | SA409XY | sa40 9xy | sa409xy | Carmarthenshire | Sir Gaerfyrddin | Llanybydder WwTW | 868 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 251995 | 244089 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA40 9YA | SA409YA | sa40 9ya | sa409ya | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 950 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 251938 | 244190 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9YB | SA409YB | sa40 9yb | sa409yb | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1363 | 1270 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.67 | 12.62 | 13.95 | 250020 | 245862 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9YD | SA409YD | sa40 9yd | sa409yd | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 865 | 1270 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.67 | 12.62 | 13.95 | 249997 | 246430 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9YE | SA409YE | sa40 9ye | sa409ye | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 631 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 249173 | 247667 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9YG | SA409YG | sa40 9yg | sa409yg | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 677 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 249156 | 247710 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9YH | SA409YH | sa40 9yh | sa409yh | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 777 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 249112 | 247800 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9YJ | SA409YJ | sa40 9yj | sa409yj | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1152 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 248769 | 248029 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9YL | SA409YL | sa40 9yl | sa409yl | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1288 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 249054 | 248325 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9YN | SA409YN | sa40 9yn | sa409yn | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1075 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 248634 | 247800 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9YP | SA409YP | sa40 9yp | sa409yp | Ceredigion | Sir Ceredigion | Gorsgoch STW | 2460 | 1416 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.39 | 14.08 | 15.56 | 247214 | 248271 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9YR | SA409YR | sa40 9yr | sa409yr | Ceredigion | Sir Ceredigion | Gorsgoch STW | 2282 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 246067 | 249010 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9YS | SA409YS | sa40 9ys | sa409ys | Ceredigion | Sir Ceredigion | Gorsgoch STW | 1863 | 1431 | 1200to1500 | 2.86 | 2.1 | 1.54 | 26.67 | 14.22 | 15.72 | 247230 | 248874 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA40 9YW | SA409YW | sa40 9yw | sa409yw | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 978 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 248799 | 247830 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA41 3PL | SA413PL | sa41 3pl | sa413pl | Pembrokeshire | Sir Benfro | Rhoshill STW | 3137 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 216169 | 239809 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA41 3PN | SA413PN | sa41 3pn | sa413pn | Pembrokeshire | Sir Benfro | Rhoshill STW | 3236 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 216065 | 240064 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA41 3PP | SA413PP | sa41 3pp | sa413pp | Pembrokeshire | Sir Benfro | Rhoshill STW | 3931 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 215398 | 239524 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA41 3PR | SA413PR | sa41 3pr | sa413pr | Pembrokeshire | Sir Benfro | Rhoshill STW | 3708 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 215637 | 240579 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA41 3PS | SA413PS | sa41 3ps | sa413ps | Pembrokeshire | Sir Benfro | Rhoshill STW | 3783 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 215690 | 241131 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA41 3PW | SA413PW | sa41 3pw | sa413pw | Pembrokeshire | Sir Benfro | Rhoshill STW | 3455 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 215907 | 240652 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 1AA | SA431AA | sa43 1aa | sa431aa | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1075 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218050 | 246447 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AB | SA431AB | sa43 1ab | sa431ab | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1127 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218076 | 246533 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AD | SA431AD | sa43 1ad | sa431ad | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1206 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218136 | 246596 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AE | SA431AE | sa43 1ae | sa431ae | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1286 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218181 | 246693 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AF | SA431AF | sa43 1af | sa431af | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1300 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218088 | 246882 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AG | SA431AG | sa43 1ag | sa431ag | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1397 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218235 | 246829 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AH | SA431AH | sa43 1ah | sa431ah | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1459 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218290 | 246858 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AJ | SA431AJ | sa43 1aj | sa431aj | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1446 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218322 | 246769 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AL | SA431AL | sa43 1al | sa431al | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1344 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218042 | 247013 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AN | SA431AN | sa43 1an | sa431an | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1206 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218086 | 246705 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AP | SA431AP | sa43 1ap | sa431ap | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1424 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218105 | 247062 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AQ | SA431AQ | sa43 1aq | sa431aq | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1474 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218271 | 246919 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AR | SA431AR | sa43 1ar | sa431ar | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1559 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218335 | 246978 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AS | SA431AS | sa43 1as | sa431as | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1662 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218420 | 247036 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AT | SA431AT | sa43 1at | sa431at | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1537 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218295 | 246998 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AU | SA431AU | sa43 1au | sa431au | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1544 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218259 | 247062 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AW | SA431AW | sa43 1aw | sa431aw | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1416 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218170 | 246966 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AX | SA431AX | sa43 1ax | sa431ax | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1644 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218356 | 247098 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AY | SA431AY | sa43 1ay | sa431ay | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1651 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218462 | 246945 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1AZ | SA431AZ | sa43 1az | sa431az | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1706 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218504 | 246981 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BA | SA431BA | sa43 1ba | sa431ba | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1704 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218427 | 247102 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BB | SA431BB | sa43 1bb | sa431bb | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1797 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218545 | 247091 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BD | SA431BD | sa43 1bd | sa431bd | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1554 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218350 | 246943 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BE | SA431BE | sa43 1be | sa431be | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1541 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218372 | 246880 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BG | SA431BG | sa43 1bg | sa431bg | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1519 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218423 | 246723 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BH | SA431BH | sa43 1bh | sa431bh | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1434 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218353 | 246669 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BJ | SA431BJ | sa43 1bj | sa431bj | Ceredigion | Sir Ceredigion | Cardigan WwTW | 969 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217939 | 246447 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BN | SA431BN | sa43 1bn | sa431bn | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1871 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218609 | 247128 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BQ | SA431BQ | sa43 1bq | sa431bq | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1539 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218415 | 246789 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BR | SA431BR | sa43 1br | sa431br | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1033 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218032 | 246348 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BS | SA431BS | sa43 1bs | sa431bs | Ceredigion | Sir Ceredigion | Cardigan WwTW | 979 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217995 | 246050 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BT | SA431BT | sa43 1bt | sa431bt | Ceredigion | Sir Ceredigion | Cardigan WwTW | 926 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217945 | 246088 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BU | SA431BU | sa43 1bu | sa431bu | Ceredigion | Sir Ceredigion | Cardigan WwTW | 895 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217915 | 246127 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BX | SA431BX | sa43 1bx | sa431bx | Ceredigion | Sir Ceredigion | Cardigan WwTW | 903 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217923 | 246125 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BY | SA431BY | sa43 1by | sa431by | Ceredigion | Sir Ceredigion | Cardigan WwTW | 843 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217862 | 246183 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1BZ | SA431BZ | sa43 1bz | sa431bz | Ceredigion | Sir Ceredigion | Cardigan WwTW | 814 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217834 | 246137 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DB | SA431DB | sa43 1db | sa431db | Ceredigion | Sir Ceredigion | Cardigan WwTW | 828 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217846 | 246081 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DD | SA431DD | sa43 1dd | sa431dd | Ceredigion | Sir Ceredigion | Cardigan WwTW | 937 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217952 | 246045 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DF | SA431DF | sa43 1df | sa431df | Ceredigion | Sir Ceredigion | Cardigan WwTW | 903 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217919 | 246054 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DG | SA431DG | sa43 1dg | sa431dg | Ceredigion | Sir Ceredigion | Cardigan WwTW | 915 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217934 | 246096 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DH | SA431DH | sa43 1dh | sa431dh | Ceredigion | Sir Ceredigion | Cardigan WwTW | 932 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217943 | 246011 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DJ | SA431DJ | sa43 1dj | sa431dj | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1009 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218021 | 246011 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DL | SA431DL | sa43 1dl | sa431dl | Ceredigion | Sir Ceredigion | Cardigan WwTW | 989 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217998 | 245994 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DN | SA431DN | sa43 1dn | sa431dn | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1018 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218038 | 246110 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DQ | SA431DQ | sa43 1dq | sa431dq | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1319 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218335 | 246247 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DR | SA431DR | sa43 1dr | sa431dr | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1341 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218361 | 246106 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DS | SA431DS | sa43 1ds | sa431ds | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1358 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218358 | 246371 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DT | SA431DT | sa43 1dt | sa431dt | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1455 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218461 | 246343 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DU | SA431DU | sa43 1du | sa431du | Ceredigion | Sir Ceredigion | Cardigan WwTW | 952 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217972 | 246153 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DW | SA431DW | sa43 1dw | sa431dw | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1108 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218127 | 246101 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DX | SA431DX | sa43 1dx | sa431dx | Ceredigion | Sir Ceredigion | Cardigan WwTW | 933 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217953 | 246147 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1DY | SA431DY | sa43 1dy | sa431dy | Ceredigion | Sir Ceredigion | Cardigan WwTW | 930 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217950 | 246161 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EA | SA431EA | sa43 1ea | sa431ea | Ceredigion | Sir Ceredigion | Cardigan WwTW | 938 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217953 | 246238 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EB | SA431EB | sa43 1eb | sa431eb | Ceredigion | Sir Ceredigion | Cardigan WwTW | 927 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217938 | 246271 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1ED | SA431ED | sa43 1ed | sa431ed | Ceredigion | Sir Ceredigion | Cardigan WwTW | 981 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217987 | 246307 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EE | SA431EE | sa43 1ee | sa431ee | Ceredigion | Sir Ceredigion | Cardigan WwTW | 960 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217955 | 246356 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EF | SA431EF | sa43 1ef | sa431ef | Ceredigion | Sir Ceredigion | Cardigan WwTW | 960 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217955 | 246356 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EG | SA431EG | sa43 1eg | sa431eg | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1126 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218128 | 246340 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EH | SA431EH | sa43 1eh | sa431eh | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1075 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218091 | 246232 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EJ | SA431EJ | sa43 1ej | sa431ej | Ceredigion | Sir Ceredigion | Cardigan WwTW | 955 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217971 | 246222 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EL | SA431EL | sa43 1el | sa431el | Ceredigion | Sir Ceredigion | Cardigan WwTW | 879 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217896 | 246211 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EN | SA431EN | sa43 1en | sa431en | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1252 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 217978 | 246946 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EQ | SA431EQ | sa43 1eq | sa431eq | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1236 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218232 | 246382 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1ER | SA431ER | sa43 1er | sa431er | Ceredigion | Sir Ceredigion | Verwig STW | 3105 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 220890 | 247738 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1ES | SA431ES | sa43 1es | sa431es | Ceredigion | Sir Ceredigion | Cardigan WwTW | 834 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217852 | 246198 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1ET | SA431ET | sa43 1et | sa431et | Ceredigion | Sir Ceredigion | Cardigan WwTW | 875 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217884 | 246002 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EW | SA431EW | sa43 1ew | sa431ew | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1603 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 218620 | 246241 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EX | SA431EX | sa43 1ex | sa431ex | Ceredigion | Sir Ceredigion | Cardigan WwTW | 891 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217893 | 245961 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EY | SA431EY | sa43 1ey | sa431ey | Ceredigion | Sir Ceredigion | Cardigan WwTW | 874 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217873 | 245951 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1EZ | SA431EZ | sa43 1ez | sa431ez | Ceredigion | Sir Ceredigion | Cardigan WwTW | 708 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217687 | 245903 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1FA | SA431FA | sa43 1fa | sa431fa | Ceredigion | Sir Ceredigion | Cardigan WwTW | 858 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217864 | 245984 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1FB | SA431FB | sa43 1fb | sa431fb | Ceredigion | Sir Ceredigion | Verwig STW | 3285 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 221201 | 247918 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1FD | SA431FD | sa43 1fd | sa431fd | Ceredigion | Sir Ceredigion | Verwig STW | 3113 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 221004 | 247914 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1FF | SA431FF | sa43 1ff | sa431ff | Ceredigion | Sir Ceredigion | Verwig STW | 3118 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 221010 | 247914 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1FG | SA431FG | sa43 1fg | sa431fg | Ceredigion | Sir Ceredigion | Verwig STW | 3118 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 221010 | 247914 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HA | SA431HA | sa43 1ha | sa431ha | Ceredigion | Sir Ceredigion | Cardigan WwTW | 784 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217791 | 246000 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HB | SA431HB | sa43 1hb | sa431hb | Ceredigion | Sir Ceredigion | Cardigan WwTW | 804 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217815 | 246020 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HD | SA431HD | sa43 1hd | sa431hd | Ceredigion | Sir Ceredigion | Cardigan WwTW | 786 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217798 | 246031 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HE | SA431HE | sa43 1he | sa431he | Ceredigion | Sir Ceredigion | Cardigan WwTW | 754 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217757 | 245981 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HH | SA431HH | sa43 1hh | sa431hh | Ceredigion | Sir Ceredigion | Cardigan WwTW | 747 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217758 | 246024 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HJ | SA431HJ | sa43 1hj | sa431hj | Ceredigion | Sir Ceredigion | Cardigan WwTW | 717 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217728 | 246029 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HL | SA431HL | sa43 1hl | sa431hl | Ceredigion | Sir Ceredigion | Cardigan WwTW | 699 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217705 | 246001 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HN | SA431HN | sa43 1hn | sa431hn | Ceredigion | Sir Ceredigion | Cardigan WwTW | 689 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217705 | 246065 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HP | SA431HP | sa43 1hp | sa431hp | Ceredigion | Sir Ceredigion | Cardigan WwTW | 644 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217654 | 246027 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HR | SA431HR | sa43 1hr | sa431hr | Ceredigion | Sir Ceredigion | Cardigan WwTW | 622 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217612 | 245949 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HS | SA431HS | sa43 1hs | sa431hs | Ceredigion | Sir Ceredigion | Cardigan WwTW | 671 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217665 | 245955 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HU | SA431HU | sa43 1hu | sa431hu | Ceredigion | Sir Ceredigion | Cardigan WwTW | 700 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217699 | 245969 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HW | SA431HW | sa43 1hw | sa431hw | Ceredigion | Sir Ceredigion | Cardigan WwTW | 628 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217643 | 246063 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HX | SA431HX | sa43 1hx | sa431hx | Ceredigion | Sir Ceredigion | Cardigan WwTW | 737 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217720 | 245908 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1HY | SA431HY | sa43 1hy | sa431hy | Ceredigion | Sir Ceredigion | Cardigan WwTW | 732 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217719 | 245922 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JA | SA431JA | sa43 1ja | sa431ja | Ceredigion | Sir Ceredigion | Cardigan WwTW | 764 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217756 | 245934 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JD | SA431JD | sa43 1jd | sa431jd | Ceredigion | Sir Ceredigion | Cardigan WwTW | 831 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217810 | 246397 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JG | SA431JG | sa43 1jg | sa431jg | Ceredigion | Sir Ceredigion | Cardigan WwTW | 752 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217771 | 246093 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JH | SA431JH | sa43 1jh | sa431jh | Ceredigion | Sir Ceredigion | Cardigan WwTW | 749 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217767 | 246087 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JJ | SA431JJ | sa43 1jj | sa431jj | Ceredigion | Sir Ceredigion | Cardigan WwTW | 731 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217751 | 246125 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JL | SA431JL | sa43 1jl | sa431jl | Ceredigion | Sir Ceredigion | Cardigan WwTW | 781 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217796 | 246230 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JN | SA431JN | sa43 1jn | sa431jn | Ceredigion | Sir Ceredigion | Cardigan WwTW | 721 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217737 | 246067 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JR | SA431JR | sa43 1jr | sa431jr | Ceredigion | Sir Ceredigion | Cardigan WwTW | 792 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217810 | 246194 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JS | SA431JS | sa43 1js | sa431js | Ceredigion | Sir Ceredigion | Cardigan WwTW | 853 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217861 | 246280 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JT | SA431JT | sa43 1jt | sa431jt | Ceredigion | Sir Ceredigion | Cardigan WwTW | 877 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217874 | 246340 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JU | SA431JU | sa43 1ju | sa431ju | Ceredigion | Sir Ceredigion | Cardigan WwTW | 945 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217934 | 246382 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JW | SA431JW | sa43 1jw | sa431jw | Ceredigion | Sir Ceredigion | Cardigan WwTW | 724 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217742 | 246091 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JX | SA431JX | sa43 1jx | sa431jx | Ceredigion | Sir Ceredigion | Cardigan WwTW | 870 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 217671 | 246717 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JY | SA431JY | sa43 1jy | sa431jy | Ceredigion | Sir Ceredigion | Cardigan WwTW | 904 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217873 | 246439 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1JZ | SA431JZ | sa43 1jz | sa431jz | Ceredigion | Sir Ceredigion | Cardigan WwTW | 990 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 217876 | 246638 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1LA | SA431LA | sa43 1la | sa431la | Ceredigion | Sir Ceredigion | Cardigan WwTW | 932 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217929 | 246346 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1LB | SA431LB | sa43 1lb | sa431lb | Ceredigion | Sir Ceredigion | Cardigan WwTW | 628 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217635 | 246266 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1LD | SA431LD | sa43 1ld | sa431ld | Ceredigion | Sir Ceredigion | Cardigan WwTW | 638 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217630 | 246328 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1LE | SA431LE | sa43 1le | sa431le | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1014 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218028 | 246034 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1LH | SA431LH | sa43 1lh | sa431lh | Ceredigion | Sir Ceredigion | Cardigan WwTW | 688 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217704 | 246218 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1LJ | SA431LJ | sa43 1lj | sa431lj | Ceredigion | Sir Ceredigion | Cardigan WwTW | 682 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217702 | 246146 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1LL | SA431LL | sa43 1ll | sa431ll | Ceredigion | Sir Ceredigion | Cardigan WwTW | 731 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217751 | 246154 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1LS | SA431LS | sa43 1ls | sa431ls | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1073 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218056 | 246420 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1LT | SA431LT | sa43 1lt | sa431lt | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1245 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218216 | 246487 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1LU | SA431LU | sa43 1lu | sa431lu | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1559 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218486 | 246670 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1LY | SA431LY | sa43 1ly | sa431ly | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1492 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218435 | 246612 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1LZ | SA431LZ | sa43 1lz | sa431lz | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1710 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218632 | 246710 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NA | SA431NA | sa43 1na | sa431na | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1755 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218647 | 246798 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NB | SA431NB | sa43 1nb | sa431nb | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1849 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218659 | 246995 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1ND | SA431ND | sa43 1nd | sa431nd | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1885 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218692 | 247010 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NE | SA431NE | sa43 1ne | sa431ne | Ceredigion | Sir Ceredigion | Cardigan WwTW | 2020 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218875 | 246940 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NF | SA431NF | sa43 1nf | sa431nf | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1923 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218785 | 246903 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NG | SA431NG | sa43 1ng | sa431ng | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1732 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218572 | 246909 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NH | SA431NH | sa43 1nh | sa431nh | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1914 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218733 | 246994 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NJ | SA431NJ | sa43 1nj | sa431nj | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1653 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218533 | 246806 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NL | SA431NL | sa43 1nl | sa431nl | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1709 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218658 | 246627 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NN | SA431NN | sa43 1nn | sa431nn | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1733 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218638 | 246761 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NP | SA431NP | sa43 1np | sa431np | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1674 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218613 | 246655 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NQ | SA431NQ | sa43 1nq | sa431nq | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1778 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218600 | 246955 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NR | SA431NR | sa43 1nr | sa431nr | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1572 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218528 | 246583 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NS | SA431NS | sa43 1ns | sa431ns | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1557 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 218537 | 246489 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NT | SA431NT | sa43 1nt | sa431nt | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1359 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218337 | 246476 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1NU | SA431NU | sa43 1nu | sa431nu | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1939 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218695 | 247117 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PA | SA431PA | sa43 1pa | sa431pa | Ceredigion | Sir Ceredigion | Cardigan WwTW | 365 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 217353 | 246290 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PE | SA431PE | sa43 1pe | sa431pe | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1279 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 217905 | 247063 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PF | SA431PF | sa43 1pf | sa431pf | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1270 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 217955 | 247000 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PG | SA431PG | sa43 1pg | sa431pg | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1801 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218454 | 247229 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PH | SA431PH | sa43 1ph | sa431ph | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1433 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 217869 | 247295 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PJ | SA431PJ | sa43 1pj | sa431pj | Ceredigion | Sir Ceredigion | Verwig STW | 1660 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 217803 | 247830 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PL | SA431PL | sa43 1pl | sa431pl | Ceredigion | Sir Ceredigion | Verwig STW | 870 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 217975 | 248605 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PN | SA431PN | sa43 1pn | sa431pn | Ceredigion | Sir Ceredigion | Verwig STW | 1665 | 963 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.95 | 9.57 | 10.58 | 217115 | 248231 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PQ | SA431PQ | sa43 1pq | sa431pq | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1804 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 218490 | 247186 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PS | SA431PS | sa43 1ps | sa431ps | Ceredigion | Sir Ceredigion | Verwig STW | 241 | 938 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.48 | 9.32 | 10.31 | 218117 | 249597 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PT | SA431PT | sa43 1pt | sa431pt | Ceredigion | Sir Ceredigion | Verwig STW | 277 | 938 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.48 | 9.32 | 10.31 | 218041 | 249561 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PW | SA431PW | sa43 1pw | sa431pw | Ceredigion | Sir Ceredigion | Verwig STW | 1571 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 216956 | 248574 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PX | SA431PX | sa43 1px | sa431px | Ceredigion | Sir Ceredigion | Verwig STW | 162 | 938 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.48 | 9.32 | 10.31 | 218242 | 249577 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1PZ | SA431PZ | sa43 1pz | sa431pz | Ceredigion | Sir Ceredigion | Verwig STW | 405 | 938 | 900to1200 | 1.88 | 1.37 | 1.01 | 17.48 | 9.32 | 10.31 | 218454 | 249786 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1QA | SA431QA | sa43 1qa | sa431qa | Ceredigion | Sir Ceredigion | Verwig STW | 554 | 966 | 900to1200 | 1.93 | 1.41 | 1.04 | 18 | 9.6 | 10.61 | 218772 | 249675 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1QJ | SA431QJ | sa43 1qj | sa431qj | Ceredigion | Sir Ceredigion | Verwig STW | 909 | 973 | 900to1200 | 1.95 | 1.42 | 1.04 | 18.14 | 9.67 | 10.69 | 219189 | 249405 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1QR | SA431QR | sa43 1qr | sa431qr | Ceredigion | Sir Ceredigion | Verwig STW | 2537 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 220445 | 248097 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1QT | SA431QT | sa43 1qt | sa431qt | Ceredigion | Sir Ceredigion | Cardigan WwTW | 2192 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 218898 | 247270 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1QU | SA431QU | sa43 1qu | sa431qu | Ceredigion | Sir Ceredigion | Verwig STW | 2457 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 219488 | 247281 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1QX | SA431QX | sa43 1qx | sa431qx | Ceredigion | Sir Ceredigion | Verwig STW | 1895 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 219811 | 248303 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1QY | SA431QY | sa43 1qy | sa431qy | Ceredigion | Sir Ceredigion | Verwig STW | 2697 | 1030 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.2 | 10.24 | 11.32 | 219852 | 247229 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1QZ | SA431QZ | sa43 1qz | sa431qz | Ceredigion | Sir Ceredigion | Verwig STW | 2507 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 220306 | 247944 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RB | SA431RB | sa43 1rb | sa431rb | Ceredigion | Sir Ceredigion | Verwig STW | 2341 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 220173 | 248042 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RD | SA431RD | sa43 1rd | sa431rd | Ceredigion | Sir Ceredigion | Verwig STW | 2978 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 220666 | 247638 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RE | SA431RE | sa43 1re | sa431re | Ceredigion | Sir Ceredigion | Verwig STW | 2956 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 220890 | 248033 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RF | SA431RF | sa43 1rf | sa431rf | Ceredigion | Sir Ceredigion | Verwig STW | 3073 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 221036 | 248061 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RG | SA431RG | sa43 1rg | sa431rg | Ceredigion | Sir Ceredigion | Verwig STW | 3147 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 221025 | 247881 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RH | SA431RH | sa43 1rh | sa431rh | Ceredigion | Sir Ceredigion | Verwig STW | 3150 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 221160 | 248145 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RJ | SA431RJ | sa43 1rj | sa431rj | Ceredigion | Sir Ceredigion | Verwig STW | 3103 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 221099 | 248123 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RL | SA431RL | sa43 1rl | sa431rl | Ceredigion | Sir Ceredigion | Verwig STW | 3175 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 221335 | 248557 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RN | SA431RN | sa43 1rn | sa431rn | Ceredigion | Sir Ceredigion | Rhosygadair Newydd Blaenannerch | 1990 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 222592 | 249826 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RP | SA431RP | sa43 1rp | sa431rp | Ceredigion | Sir Ceredigion | Rhosygadair Newydd Blaenannerch | 1404 | 1085 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.22 | 10.79 | 11.92 | 223262 | 250265 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RQ | SA431RQ | sa43 1rq | sa431rq | Ceredigion | Sir Ceredigion | Verwig STW | 3342 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 221281 | 247950 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RR | SA431RR | sa43 1rr | sa431rr | Ceredigion | Sir Ceredigion | Rhosygadair Newydd Blaenannerch | 829 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 223982 | 250358 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RS | SA431RS | sa43 1rs | sa431rs | Ceredigion | Sir Ceredigion | Rhosygadair Newydd Blaenannerch | 99 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 224502 | 249845 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RT | SA431RT | sa43 1rt | sa431rt | Ceredigion | Sir Ceredigion | Rhosygadair Newydd Blaenannerch | 2667 | 1059 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.74 | 10.53 | 11.64 | 221996 | 250439 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RU | SA431RU | sa43 1ru | sa431ru | Ceredigion | Sir Ceredigion | Verwig STW | 2791 | 1035 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.29 | 10.29 | 11.37 | 220904 | 250371 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RW | SA431RW | sa43 1rw | sa431rw | Ceredigion | Sir Ceredigion | Rhosygadair Newydd Blaenannerch | 1858 | 1025 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.1 | 10.19 | 11.26 | 222877 | 250524 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RX | SA431RX | sa43 1rx | sa431rx | Ceredigion | Sir Ceredigion | Verwig STW | 1522 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 219797 | 249301 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RY | SA431RY | sa43 1ry | sa431ry | Ceredigion | Sir Ceredigion | Verwig STW | 2445 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 220720 | 249257 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1RZ | SA431RZ | sa43 1rz | sa431rz | Ceredigion | Sir Ceredigion | Verwig STW | 2070 | 1037 | 900to1200 | 2.08 | 1.52 | 1.11 | 19.33 | 10.31 | 11.39 | 220326 | 249108 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SA | SA431SA | sa43 1sa | sa431sa | Ceredigion | Sir Ceredigion | Verwig STW | 2544 | 1066 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.87 | 10.6 | 11.71 | 220701 | 248637 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SB | SA431SB | sa43 1sb | sa431sb | Ceredigion | Sir Ceredigion | Blaenannerch STW | 3305 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 221351 | 248086 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SD | SA431SD | sa43 1sd | sa431sd | Ceredigion | Sir Ceredigion | Verwig STW | 2914 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 220977 | 248317 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SE | SA431SE | sa43 1se | sa431se | Ceredigion | Sir Ceredigion | Verwig STW | 3195 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 221140 | 247996 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SF | SA431SF | sa43 1sf | sa431sf | Ceredigion | Sir Ceredigion | Verwig STW | 2885 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 220741 | 247914 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SG | SA431SG | sa43 1sg | sa431sg | Ceredigion | Sir Ceredigion | Blaenannerch STW | 2815 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 221830 | 248190 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SH | SA431SH | sa43 1sh | sa431sh | Ceredigion | Sir Ceredigion | Blaenannerch STW | 2306 | 1117 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.82 | 11.1 | 12.27 | 222314 | 248990 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SJ | SA431SJ | sa43 1sj | sa431sj | Ceredigion | Sir Ceredigion | Blaenannerch STW | 1415 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 223186 | 248652 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SL | SA431SL | sa43 1sl | sa431sl | Ceredigion | Sir Ceredigion | Blaenannerch STW | 1058 | 1152 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.47 | 11.45 | 12.66 | 223567 | 248918 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SN | SA431SN | sa43 1sn | sa431sn | Ceredigion | Sir Ceredigion | Blaenannerch STW | 317 | 1152 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.47 | 11.45 | 12.66 | 224495 | 248989 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SP | SA431SP | sa43 1sp | sa431sp | Ceredigion | Sir Ceredigion | Blaenannerch STW | 244 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 224541 | 248927 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SQ | SA431SQ | sa43 1sq | sa431sq | Ceredigion | Sir Ceredigion | Blaenannerch STW | 2024 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 222587 | 248482 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 1SW | SA431SW | sa43 1sw | sa431sw | Ceredigion | Sir Ceredigion | Rhosygadair Newydd Blaenannerch | 907 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 223692 | 249610 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2AA | SA432AA | sa43 2aa | sa432aa | Ceredigion | Sir Ceredigion | Llechryd STW | 3343 | 1105 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.6 | 10.98 | 12.14 | 221044 | 246677 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2AB | SA432AB | sa43 2ab | sa432ab | Ceredigion | Sir Ceredigion | Blaenannerch STW | 3583 | 1105 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.6 | 10.98 | 12.14 | 221288 | 247323 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2AD | SA432AD | sa43 2ad | sa432ad | Ceredigion | Sir Ceredigion | Blaenannerch STW | 1602 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 223279 | 247783 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2AE | SA432AE | sa43 2ae | sa432ae | Ceredigion | Sir Ceredigion | Blaenannerch STW | 2175 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 222920 | 247308 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2AF | SA432AF | sa43 2af | sa432af | Ceredigion | Sir Ceredigion | Blaenannerch STW | 2217 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 223073 | 247083 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2AG | SA432AG | sa43 2ag | sa432ag | Ceredigion | Sir Ceredigion | Blaenannerch STW | 1107 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 223697 | 248050 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2AH | SA432AH | sa43 2ah | sa432ah | Ceredigion | Sir Ceredigion | Blaenannerch STW | 323 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 224597 | 249013 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2AJ | SA432AJ | sa43 2aj | sa432aj | Ceredigion | Sir Ceredigion | Blaenannerch STW | 486 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 224368 | 248263 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2AL | SA432AL | sa43 2al | sa432al | Ceredigion | Sir Ceredigion | Blaenannerch STW | 503 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 224976 | 249024 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2AN | SA432AN | sa43 2an | sa432an | Ceredigion | Sir Ceredigion | Blaenannerch STW | 1014 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 225518 | 249120 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2AQ | SA432AQ | sa43 2aq | sa432aq | Pembrokeshire | Sir Benfro | Cilgerran STW | 892 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 220182 | 242689 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2AR | SA432AR | sa43 2ar | sa432ar | Ceredigion | Sir Ceredigion | Blaenannerch STW | 1917 | 1254 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.37 | 12.47 | 13.78 | 226471 | 248274 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2BG | SA432BG | sa43 2bg | sa432bg | Ceredigion | Sir Ceredigion | Blaenannerch STW | 1454 | 1254 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.37 | 12.47 | 13.78 | 225720 | 247763 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2BN | SA432BN | sa43 2bn | sa432bn | Ceredigion | Sir Ceredigion | Rhosygadair Newydd Blaenannerch | 345 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 224578 | 249441 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2BP | SA432BP | sa43 2bp | sa432bp | Ceredigion | Sir Ceredigion | Rhosygadair Newydd Blaenannerch | 157 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 224553 | 249940 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2BQ | SA432BQ | sa43 2bq | sa432bq | Ceredigion | Sir Ceredigion | Blaenannerch STW | 880 | 1235 | 1200to1500 | 2.47 | 1.81 | 1.33 | 23.02 | 12.28 | 13.57 | 224852 | 247847 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2BW | SA432BW | sa43 2bw | sa432bw | Ceredigion | Sir Ceredigion | Rhosygadair Newydd Blaenannerch | 166 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 224680 | 249652 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2DZ | SA432DZ | sa43 2dz | sa432dz | Ceredigion | Sir Ceredigion | Rhosygadair Newydd Blaenannerch | 312 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 224673 | 249488 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2HP | SA432HP | sa43 2hp | sa432hp | Ceredigion | Sir Ceredigion | Blaenannerch STW | 3415 | 1159 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.6 | 11.52 | 12.73 | 227966 | 249263 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2HZ | SA432HZ | sa43 2hz | sa432hz | Ceredigion | Sir Ceredigion | Beulah WwTW | 3301 | 1159 | 900to1200 | 2.32 | 1.7 | 1.24 | 21.6 | 11.52 | 12.73 | 228142 | 249178 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2JA | SA432JA | sa43 2ja | sa432ja | Ceredigion | Sir Ceredigion | Beulah WwTW | 2822 | 1191 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.2 | 11.84 | 13.09 | 228555 | 248826 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2JB | SA432JB | sa43 2jb | sa432jb | Ceredigion | Sir Ceredigion | Beulah WwTW | 2475 | 1191 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.2 | 11.84 | 13.09 | 229250 | 248624 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2JD | SA432JD | sa43 2jd | sa432jd | Ceredigion | Sir Ceredigion | Beulah WwTW | 2344 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 228552 | 248312 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2JR | SA432JR | sa43 2jr | sa432jr | Ceredigion | Sir Ceredigion | Beulah WwTW | 3981 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 229883 | 250120 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2JS | SA432JS | sa43 2js | sa432js | Ceredigion | Sir Ceredigion | Beulah WwTW | 3451 | 1162 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.66 | 11.55 | 12.77 | 229275 | 249605 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2JT | SA432JT | sa43 2jt | sa432jt | Ceredigion | Sir Ceredigion | Beulah WwTW | 3153 | 1191 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.2 | 11.84 | 13.09 | 228764 | 249230 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LA | SA432LA | sa43 2la | sa432la | Ceredigion | Sir Ceredigion | Cardigan WwTW | 2024 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 219038 | 246300 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LB | SA432LB | sa43 2lb | sa432lb | Ceredigion | Sir Ceredigion | Cilgerran STW | 2819 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 219903 | 246027 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LD | SA432LD | sa43 2ld | sa432ld | Ceredigion | Sir Ceredigion | Cardigan WwTW | 2000 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 219001 | 245868 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LE | SA432LE | sa43 2le | sa432le | Ceredigion | Sir Ceredigion | Cilgerran STW | 2212 | 1074 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.02 | 10.68 | 11.8 | 219537 | 245451 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LF | SA432LF | sa43 2lf | sa432lf | Ceredigion | Sir Ceredigion | Cilgerran STW | 2040 | 1074 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.02 | 10.68 | 11.8 | 219948 | 245226 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LG | SA432LG | sa43 2lg | sa432lg | Ceredigion | Sir Ceredigion | Cilgerran STW | 1909 | 1074 | 900to1200 | 2.15 | 1.57 | 1.15 | 20.02 | 10.68 | 11.8 | 219814 | 245120 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LH | SA432LH | sa43 2lh | sa432lh | Ceredigion | Sir Ceredigion | Llechryd STW | 2501 | 1016 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.94 | 10.1 | 11.16 | 220283 | 245646 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LJ | SA432LJ | sa43 2lj | sa432lj | Ceredigion | Sir Ceredigion | Llechryd STW | 2833 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 220855 | 246145 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LL | SA432LL | sa43 2ll | sa432ll | Ceredigion | Sir Ceredigion | Llechryd STW | 3214 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 222227 | 246402 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LN | SA432LN | sa43 2ln | sa432ln | Ceredigion | Sir Ceredigion | Blaenannerch STW | 2900 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 222208 | 247051 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LP | SA432LP | sa43 2lp | sa432lp | Ceredigion | Sir Ceredigion | Llechryd STW | 2380 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 220838 | 245684 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LQ | SA432LQ | sa43 2lq | sa432lq | Ceredigion | Sir Ceredigion | Cilgerran STW | 252 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219477 | 243492 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LR | SA432LR | sa43 2lr | sa432lr | Ceredigion | Sir Ceredigion | Llechryd STW | 2710 | 1106 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.61 | 10.99 | 12.15 | 221830 | 245987 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LS | SA432LS | sa43 2ls | sa432ls | Ceredigion | Sir Ceredigion | Llechryd STW | 3070 | 1121 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.89 | 11.14 | 12.32 | 223060 | 245820 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LT | SA432LT | sa43 2lt | sa432lt | Ceredigion | Sir Ceredigion | Llechryd STW | 2118 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 222611 | 244963 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LU | SA432LU | sa43 2lu | sa432lu | Ceredigion | Sir Ceredigion | Llechryd STW | 1554 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 222442 | 244337 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LX | SA432LX | sa43 2lx | sa432lx | Ceredigion | Sir Ceredigion | Llechryd STW | 2505 | 1100 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.5 | 10.93 | 12.09 | 222979 | 245153 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LY | SA432LY | sa43 2ly | sa432ly | Ceredigion | Sir Ceredigion | Blaenannerch STW | 2892 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 224084 | 245844 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2LZ | SA432LZ | sa43 2lz | sa432lz | Ceredigion | Sir Ceredigion | Blaenannerch STW | 3277 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 224215 | 245436 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NA | SA432NA | sa43 2na | sa432na | Ceredigion | Sir Ceredigion | Blaenannerch STW | 2531 | 1191 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.2 | 11.84 | 13.09 | 225038 | 246197 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NB | SA432NB | sa43 2nb | sa432nb | Ceredigion | Sir Ceredigion | Blaenannerch STW | 2817 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 223939 | 245952 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2ND | SA432ND | sa43 2nd | sa432nd | Ceredigion | Sir Ceredigion | Blaenannerch STW | 2048 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 224276 | 246668 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NE | SA432NE | sa43 2ne | sa432ne | Ceredigion | Sir Ceredigion | Llechryd STW | 1144 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 221195 | 244483 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NG | SA432NG | sa43 2ng | sa432ng | Ceredigion | Sir Ceredigion | Llechryd STW | 974 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 221087 | 244300 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NH | SA432NH | sa43 2nh | sa432nh | Ceredigion | Sir Ceredigion | Llechryd STW | 1588 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 220504 | 244742 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NJ | SA432NJ | sa43 2nj | sa432nj | Ceredigion | Sir Ceredigion | Llechryd STW | 1076 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 221058 | 244399 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NL | SA432NL | sa43 2nl | sa432nl | Ceredigion | Sir Ceredigion | Llechryd STW | 983 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 221266 | 244323 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NN | SA432NN | sa43 2nn | sa432nn | Ceredigion | Sir Ceredigion | Llechryd STW | 813 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 221446 | 244129 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NP | SA432NP | sa43 2np | sa432np | Ceredigion | Sir Ceredigion | Llechryd STW | 742 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 221548 | 244020 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NQ | SA432NQ | sa43 2nq | sa432nq | Ceredigion | Sir Ceredigion | Llechryd STW | 899 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 221230 | 244239 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NR | SA432NR | sa43 2nr | sa432nr | Ceredigion | Sir Ceredigion | Llechryd STW | 646 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 221657 | 243842 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NS | SA432NS | sa43 2ns | sa432ns | Ceredigion | Sir Ceredigion | Llechryd STW | 850 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 221305 | 244188 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NT | SA432NT | sa43 2nt | sa432nt | Ceredigion | Sir Ceredigion | Llechryd STW | 640 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 221727 | 243766 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NU | SA432NU | sa43 2nu | sa432nu | Ceredigion | Sir Ceredigion | Llechryd STW | 718 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 221845 | 243741 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NW | SA432NW | sa43 2nw | sa432nw | Ceredigion | Sir Ceredigion | Llechryd STW | 839 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 221539 | 244128 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NX | SA432NX | sa43 2nx | sa432nx | Ceredigion | Sir Ceredigion | Llechryd STW | 677 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 221766 | 243778 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NY | SA432NY | sa43 2ny | sa432ny | Ceredigion | Sir Ceredigion | Llechryd STW | 1101 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 221181 | 244439 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2NZ | SA432NZ | sa43 2nz | sa432nz | Ceredigion | Sir Ceredigion | Llechryd STW | 445 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 221327 | 243778 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2PA | SA432PA | sa43 2pa | sa432pa | Ceredigion | Sir Ceredigion | Llechryd STW | 536 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 220725 | 243234 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2PB | SA432PB | sa43 2pb | sa432pb | Ceredigion | Sir Ceredigion | Llechryd STW | 1026 | 1076 | 900to1200 | 2.15 | 1.58 | 1.16 | 20.05 | 10.7 | 11.82 | 220488 | 244027 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2PD | SA432PD | sa43 2pd | sa432pd | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 469 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 220657 | 242753 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2PE | SA432PE | sa43 2pe | sa432pe | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 693 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 220465 | 242323 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2PF | SA432PF | sa43 2pf | sa432pf | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 953 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 220214 | 242248 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2PG | SA432PG | sa43 2pg | sa432pg | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 374 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 221205 | 242241 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2PH | SA432PH | sa43 2ph | sa432ph | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 1002 | 1120 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.88 | 11.13 | 12.31 | 221969 | 242102 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2PJ | SA432PJ | sa43 2pj | sa432pj | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 1504 | 1120 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.88 | 11.13 | 12.31 | 222443 | 241924 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2PL | SA432PL | sa43 2pl | sa432pl | Pembrokeshire | Sir Benfro | Abercych WwTW | 1080 | 1083 | 900to1200 | 2.17 | 1.59 | 1.16 | 20.19 | 10.77 | 11.9 | 223670 | 242049 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2PN | SA432PN | sa43 2pn | sa432pn | Pembrokeshire | Sir Benfro | Llechryd STW | 2015 | 1086 | 900to1200 | 2.17 | 1.59 | 1.17 | 20.24 | 10.8 | 11.93 | 223228 | 242958 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2PP | SA432PP | sa43 2pp | sa432pp | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 920 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 221403 | 241731 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2PQ | SA432PQ | sa43 2pq | sa432pq | Ceredigion | Sir Ceredigion | Llechryd STW | 920 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 221496 | 244226 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2PR | SA432PR | sa43 2pr | sa432pr | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 1256 | 1140 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.25 | 11.33 | 12.53 | 221015 | 241347 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2PS | SA432PS | sa43 2ps | sa432ps | Ceredigion | Sir Ceredigion | Llechryd STW | 1271 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 222062 | 244318 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2PT | SA432PT | sa43 2pt | sa432pt | Ceredigion | Sir Ceredigion | Llechryd STW | 1597 | 1114 | 900to1200 | 2.23 | 1.63 | 1.2 | 20.76 | 11.07 | 12.24 | 220614 | 244805 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2PY | SA432PY | sa43 2py | sa432py | Ceredigion | Sir Ceredigion | Llechryd STW | 1112 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 222188 | 243938 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QA | SA432QA | sa43 2qa | sa432qa | Pembrokeshire | Sir Benfro | Llechryd STW | 259 | 1071 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.96 | 10.65 | 11.77 | 221345 | 243581 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2QB | SA432QB | sa43 2qb | sa432qb | Pembrokeshire | Sir Benfro | Llechryd STW | 599 | 1070 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.94 | 10.64 | 11.76 | 221706 | 242952 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2QD | SA432QD | sa43 2qd | sa432qd | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 381 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 221413 | 242817 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2QE | SA432QE | sa43 2qe | sa432qe | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 1017 | 1120 | 900to1200 | 2.24 | 1.64 | 1.2 | 20.88 | 11.13 | 12.31 | 221847 | 241910 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2QG | SA432QG | sa43 2qg | sa432qg | Ceredigion | Sir Ceredigion | Llechryd STW | 946 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 222022 | 243887 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QH | SA432QH | sa43 2qh | sa432qh | Ceredigion | Sir Ceredigion | Llechryd STW | 1286 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 222116 | 244291 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QJ | SA432QJ | sa43 2qj | sa432qj | Ceredigion | Sir Ceredigion | Llechryd STW | 1027 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 222163 | 243810 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QL | SA432QL | sa43 2ql | sa432ql | Ceredigion | Sir Ceredigion | Llechryd STW | 1382 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 222602 | 243626 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QN | SA432QN | sa43 2qn | sa432qn | Ceredigion | Sir Ceredigion | Llechryd STW | 1983 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 223210 | 243644 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QP | SA432QP | sa43 2qp | sa432qp | Ceredigion | Sir Ceredigion | Abercych WwTW | 2147 | 1092 | 900to1200 | 2.19 | 1.6 | 1.17 | 20.35 | 10.86 | 12 | 223943 | 243316 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QQ | SA432QQ | sa43 2qq | sa432qq | Ceredigion | Sir Ceredigion | Llechryd STW | 928 | 1062 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.79 | 10.56 | 11.67 | 222061 | 243791 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QR | SA432QR | sa43 2qr | sa432qr | Ceredigion | Sir Ceredigion | Llechryd STW | 2517 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 223722 | 243814 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QS | SA432QS | sa43 2qs | sa432qs | Ceredigion | Sir Ceredigion | Llechryd STW | 3000 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 224111 | 244241 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QT | SA432QT | sa43 2qt | sa432qt | Ceredigion | Sir Ceredigion | Abercych WwTW | 2517 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 224072 | 243710 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QU | SA432QU | sa43 2qu | sa432qu | Ceredigion | Sir Ceredigion | Abercych WwTW | 2422 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 224258 | 243628 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QW | SA432QW | sa43 2qw | sa432qw | Ceredigion | Sir Ceredigion | Llechryd STW | 2186 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 223429 | 243510 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QX | SA432QX | sa43 2qx | sa432qx | Ceredigion | Sir Ceredigion | Abercych WwTW | 2515 | 1125 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.97 | 11.18 | 12.36 | 224523 | 243717 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2QY | SA432QY | sa43 2qy | sa432qy | Ceredigion | Sir Ceredigion | Cenarth WwTW | 2031 | 1148 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.4 | 11.41 | 12.61 | 225787 | 243532 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2RA | SA432RA | sa43 2ra | sa432ra | Ceredigion | Sir Ceredigion | Cenarth WwTW | 3025 | 1125 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.97 | 11.18 | 12.36 | 225426 | 244459 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2RB | SA432RB | sa43 2rb | sa432rb | Ceredigion | Sir Ceredigion | Cenarth WwTW | 3428 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 225617 | 244952 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2RD | SA432RD | sa43 2rd | sa432rd | Ceredigion | Sir Ceredigion | Blaenannerch STW | 3295 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 225777 | 245613 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2RE | SA432RE | sa43 2re | sa432re | Ceredigion | Sir Ceredigion | Beulah WwTW | 3339 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 226179 | 245660 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2RF | SA432RF | sa43 2rf | sa432rf | Ceredigion | Sir Ceredigion | Blaenannerch STW | 2759 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 225838 | 246224 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2RG | SA432RG | sa43 2rg | sa432rg | Pembrokeshire | Sir Benfro | Rhoshill STW | 1176 | 1169 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.79 | 11.62 | 12.84 | 219819 | 241055 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2RH | SA432RH | sa43 2rh | sa432rh | Ceredigion | Sir Ceredigion | Blaenannerch STW | 1821 | 1230 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.93 | 12.23 | 13.51 | 224996 | 246913 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2RJ | SA432RJ | sa43 2rj | sa432rj | Ceredigion | Sir Ceredigion | Beulah WwTW | 3390 | 1151 | 900to1200 | 2.3 | 1.69 | 1.24 | 21.45 | 11.44 | 12.65 | 226255 | 245117 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2RL | SA432RL | sa43 2rl | sa432rl | Ceredigion | Sir Ceredigion | Cenarth WwTW | 2403 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 226777 | 244057 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2RN | SA432RN | sa43 2rn | sa432rn | Ceredigion | Sir Ceredigion | Abercych WwTW | 3198 | 1125 | 900to1200 | 2.25 | 1.65 | 1.21 | 20.97 | 11.18 | 12.36 | 224684 | 244388 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2RP | SA432RP | sa43 2rp | sa432rp | Ceredigion | Sir Ceredigion | Llechryd STW | 2659 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 223746 | 244258 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2RS | SA432RS | sa43 2rs | sa432rs | Pembrokeshire | Sir Benfro | Cilgerran STW | 694 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219966 | 242745 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2RT | SA432RT | sa43 2rt | sa432rt | Pembrokeshire | Sir Benfro | Cilgerran STW | 725 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219993 | 242728 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2RU | SA432RU | sa43 2ru | sa432ru | Pembrokeshire | Sir Benfro | Cilgerran STW | 233 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219562 | 243022 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2RW | SA432RW | sa43 2rw | sa432rw | Ceredigion | Sir Ceredigion | Llechryd STW | 3346 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 224256 | 244810 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 2RX | SA432RX | sa43 2rx | sa432rx | Pembrokeshire | Sir Benfro | Cilgerran STW | 1522 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 218008 | 242854 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2RY | SA432RY | sa43 2ry | sa432ry | Pembrokeshire | Sir Benfro | Cilgerran STW | 811 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 218708 | 242991 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2RZ | SA432RZ | sa43 2rz | sa432rz | Pembrokeshire | Sir Benfro | Cilgerran STW | 618 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 218946 | 242929 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SA | SA432SA | sa43 2sa | sa432sa | Pembrokeshire | Sir Benfro | Cilgerran STW | 355 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219269 | 242954 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SB | SA432SB | sa43 2sb | sa432sb | Pembrokeshire | Sir Benfro | Cilgerran STW | 278 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219372 | 242984 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SD | SA432SD | sa43 2sd | sa432sd | Pembrokeshire | Sir Benfro | Cilgerran STW | 210 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219405 | 243044 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SE | SA432SE | sa43 2se | sa432se | Pembrokeshire | Sir Benfro | Cilgerran STW | 197 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219437 | 243048 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SF | SA432SF | sa43 2sf | sa432sf | Pembrokeshire | Sir Benfro | Cilgerran STW | 152 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219451 | 243091 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SG | SA432SG | sa43 2sg | sa432sg | Pembrokeshire | Sir Benfro | Cilgerran STW | 262 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219521 | 242981 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SH | SA432SH | sa43 2sh | sa432sh | Pembrokeshire | Sir Benfro | Cilgerran STW | 445 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219183 | 242908 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SL | SA432SL | sa43 2sl | sa432sl | Pembrokeshire | Sir Benfro | Cilgerran STW | 431 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219665 | 242851 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SN | SA432SN | sa43 2sn | sa432sn | Pembrokeshire | Sir Benfro | Cilgerran STW | 629 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219933 | 242804 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SQ | SA432SQ | sa43 2sq | sa432sq | Pembrokeshire | Sir Benfro | Cilgerran STW | 305 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219532 | 242939 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SR | SA432SR | sa43 2sr | sa432sr | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 871 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 220246 | 242773 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SS | SA432SS | sa43 2ss | sa432ss | Pembrokeshire | Sir Benfro | Cilgerran STW | 312 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219627 | 242965 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SU | SA432SU | sa43 2su | sa432su | Pembrokeshire | Sir Benfro | Cilgerran STW | 255 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219271 | 243094 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SW | SA432SW | sa43 2sw | sa432sw | Pembrokeshire | Sir Benfro | Cilgerran STW | 877 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 220120 | 242641 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SX | SA432SX | sa43 2sx | sa432sx | Pembrokeshire | Sir Benfro | Cilgerran STW | 329 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219218 | 243041 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SY | SA432SY | sa43 2sy | sa432sy | Pembrokeshire | Sir Benfro | Cilgerran STW | 258 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219302 | 243053 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2SZ | SA432SZ | sa43 2sz | sa432sz | Pembrokeshire | Sir Benfro | Cilgerran STW | 457 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219031 | 243156 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TA | SA432TA | sa43 2ta | sa432ta | Pembrokeshire | Sir Benfro | Cilgerran STW | 349 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219142 | 243152 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TB | SA432TB | sa43 2tb | sa432tb | Pembrokeshire | Sir Benfro | Cilgerran STW | 1715 | 1042 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.42 | 10.36 | 11.45 | 218536 | 244672 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TD | SA432TD | sa43 2td | sa432td | Pembrokeshire | Sir Benfro | Cilgerran STW | 621 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 218887 | 243054 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TE | SA432TE | sa43 2te | sa432te | Pembrokeshire | Sir Benfro | Cilgerran STW | 631 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219912 | 242780 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TF | SA432TF | sa43 2tf | sa432tf | Pembrokeshire | Sir Benfro | Cilgerran STW | 491 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219665 | 242785 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TG | SA432TG | sa43 2tg | sa432tg | Pembrokeshire | Sir Benfro | Cilgerran STW | 576 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219830 | 242782 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TH | SA432TH | sa43 2th | sa432th | Pembrokeshire | Sir Benfro | Cilgerran STW | 636 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219596 | 242615 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TJ | SA432TJ | sa43 2tj | sa432tj | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 1079 | 1091 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.33 | 10.85 | 11.99 | 220109 | 242174 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TL | SA432TL | sa43 2tl | sa432tl | Pembrokeshire | Sir Benfro | Rhoshill STW | 1151 | 1169 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.79 | 11.62 | 12.84 | 219697 | 241080 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TN | SA432TN | sa43 2tn | sa432tn | Pembrokeshire | Sir Benfro | Rhoshill STW | 810 | 1228 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.89 | 12.21 | 13.49 | 219486 | 240788 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TP | SA432TP | sa43 2tp | sa432tp | Pembrokeshire | Sir Benfro | Pontrhydyceirt STW | 1274 | 1140 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.25 | 11.33 | 12.53 | 220631 | 241415 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TQ | SA432TQ | sa43 2tq | sa432tq | Pembrokeshire | Sir Benfro | Cilgerran STW | 611 | 1069 | 900to1200 | 2.14 | 1.57 | 1.15 | 19.92 | 10.63 | 11.74 | 219845 | 242750 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TR | SA432TR | sa43 2tr | sa432tr | Pembrokeshire | Sir Benfro | Rhoshill STW | 249 | 1326 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.71 | 13.18 | 14.57 | 219165 | 240209 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TS | SA432TS | sa43 2ts | sa432ts | Pembrokeshire | Sir Benfro | Rhoshill STW | 205 | 1326 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.71 | 13.18 | 14.57 | 219271 | 239797 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TT | SA432TT | sa43 2tt | sa432tt | Pembrokeshire | Sir Benfro | Rhoshill STW | 309 | 1326 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.71 | 13.18 | 14.57 | 219018 | 240127 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TU | SA432TU | sa43 2tu | sa432tu | Pembrokeshire | Sir Benfro | Rhoshill STW | 430 | 1326 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.71 | 13.18 | 14.57 | 218871 | 239968 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TW | SA432TW | sa43 2tw | sa432tw | Pembrokeshire | Sir Benfro | Rhoshill STW | 1144 | 1169 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.79 | 11.62 | 12.84 | 220197 | 240710 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TX | SA432TX | sa43 2tx | sa432tx | Pembrokeshire | Sir Benfro | Rhoshill STW | 1235 | 1252 | 1200to1500 | 2.51 | 1.83 | 1.34 | 23.34 | 12.45 | 13.76 | 218493 | 240935 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TY | SA432TY | sa43 2ty | sa432ty | Pembrokeshire | Sir Benfro | Cilgerran STW | 2163 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 217855 | 241813 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 2TZ | SA432TZ | sa43 2tz | sa432tz | Pembrokeshire | Sir Benfro | Cilgerran STW | 586 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 219034 | 242860 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3AA | SA433AA | sa43 3aa | sa433aa | Ceredigion | Sir Ceredigion | Cardigan WwTW | 829 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217754 | 245755 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AB | SA433AB | sa43 3ab | sa433ab | Ceredigion | Sir Ceredigion | Cardigan WwTW | 904 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217824 | 245727 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AD | SA433AD | sa43 3ad | sa433ad | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1028 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217988 | 245793 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AE | SA433AE | sa43 3ae | sa433ae | Ceredigion | Sir Ceredigion | Cardigan WwTW | 846 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217749 | 245711 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AF | SA433AF | sa43 3af | sa433af | Ceredigion | Sir Ceredigion | Cardigan WwTW | 969 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217865 | 245666 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AG | SA433AG | sa43 3ag | sa433ag | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1102 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218011 | 245659 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AH | SA433AH | sa43 3ah | sa433ah | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1172 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218007 | 245508 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AJ | SA433AJ | sa43 3aj | sa433aj | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1218 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218073 | 245528 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AL | SA433AL | sa43 3al | sa433al | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1266 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218139 | 245548 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AN | SA433AN | sa43 3an | sa433an | Ceredigion | Sir Ceredigion | Cardigan WwTW | 983 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217833 | 245588 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AP | SA433AP | sa43 3ap | sa433ap | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1068 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217880 | 245507 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AQ | SA433AQ | sa43 3aq | sa433aq | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1020 | 1020 | 900to1200 | 2.04 | 1.49 | 1.1 | 19.01 | 10.14 | 11.21 | 217804 | 245487 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AS | SA433AS | sa43 3as | sa433as | Ceredigion | Sir Ceredigion | Cardigan WwTW | 817 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217718 | 245716 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AT | SA433AT | sa43 3at | sa433at | Ceredigion | Sir Ceredigion | Cardigan WwTW | 737 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217646 | 245751 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AU | SA433AU | sa43 3au | sa433au | Ceredigion | Sir Ceredigion | Cardigan WwTW | 663 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217583 | 245789 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AW | SA433AW | sa43 3aw | sa433aw | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1218 | 1020 | 900to1200 | 2.04 | 1.49 | 1.1 | 19.01 | 10.14 | 11.21 | 217951 | 245354 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AX | SA433AX | sa43 3ax | sa433ax | Ceredigion | Sir Ceredigion | Cardigan WwTW | 579 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 217514 | 245838 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3AY | SA433AY | sa43 3ay | sa433ay | Ceredigion | Sir Ceredigion | Cardigan WwTW | 420 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 217351 | 245882 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3BA | SA433BA | sa43 3ba | sa433ba | Ceredigion | Sir Ceredigion | Cardigan WwTW | 315 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 217240 | 245914 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3BJ | SA433BJ | sa43 3bj | sa433bj | Pembrokeshire | Sir Benfro | Cardigan WwTW | 2688 | 1099 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.48 | 10.92 | 12.07 | 214825 | 244588 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3BQ | SA433BQ | sa43 3bq | sa433bq | Pembrokeshire | Sir Benfro | Cardigan WwTW | 1526 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 215638 | 245494 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DA | SA433DA | sa43 3da | sa433da | Pembrokeshire | Sir Benfro | Cardigan WwTW | 648 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 216655 | 245605 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DD | SA433DD | sa43 3dd | sa433dd | Pembrokeshire | Sir Benfro | Cilgerran STW | 2001 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 217748 | 242237 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DE | SA433DE | sa43 3de | sa433de | Pembrokeshire | Sir Benfro | Cilgerran STW | 2122 | 1153 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.49 | 11.46 | 12.67 | 217689 | 242101 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DF | SA433DF | sa43 3df | sa433df | Pembrokeshire | Sir Benfro | Rhoshill STW | 2471 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 217450 | 241638 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DG | SA433DG | sa43 3dg | sa433dg | Pembrokeshire | Sir Benfro | Rhoshill STW | 2746 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 216771 | 241070 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DH | SA433DH | sa43 3dh | sa433dh | Pembrokeshire | Sir Benfro | Rhoshill STW | 2284 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 217072 | 240504 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DJ | SA433DJ | sa43 3dj | sa433dj | Pembrokeshire | Sir Benfro | Rhoshill STW | 1581 | 1420 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.47 | 14.12 | 15.6 | 217720 | 240046 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DL | SA433DL | sa43 3dl | sa433dl | Pembrokeshire | Sir Benfro | Rhoshill STW | 2169 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 217161 | 239638 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DP | SA433DP | sa43 3dp | sa433dp | Ceredigion | Sir Ceredigion | Cardigan WwTW | 915 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 217412 | 245313 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3DQ | SA433DQ | sa43 3dq | sa433dq | Pembrokeshire | Sir Benfro | Rhoshill STW | 1902 | 1252 | 1200to1500 | 2.51 | 1.83 | 1.34 | 23.34 | 12.45 | 13.76 | 217648 | 240942 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DR | SA433DR | sa43 3dr | sa433dr | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1579 | 1020 | 900to1200 | 2.04 | 1.49 | 1.1 | 19.01 | 10.14 | 11.21 | 217779 | 244755 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3DS | SA433DS | sa43 3ds | sa433ds | Pembrokeshire | Sir Benfro | Cardigan WwTW | 1018 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 216998 | 245122 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DT | SA433DT | sa43 3dt | sa433dt | Pembrokeshire | Sir Benfro | Cardigan WwTW | 891 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 216895 | 245258 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DU | SA433DU | sa43 3du | sa433du | Pembrokeshire | Sir Benfro | Cardigan WwTW | 709 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 216659 | 245530 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DW | SA433DW | sa43 3dw | sa433dw | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1100 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 217089 | 245042 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3DX | SA433DX | sa43 3dx | sa433dx | Pembrokeshire | Sir Benfro | Cardigan WwTW | 616 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 216513 | 245790 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3DY | SA433DY | sa43 3dy | sa433dy | Pembrokeshire | Sir Benfro | Cardigan WwTW | 539 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 216523 | 245932 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EA | SA433EA | sa43 3ea | sa433ea | Pembrokeshire | Sir Benfro | Cardigan WwTW | 515 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 216529 | 245985 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EB | SA433EB | sa43 3eb | sa433eb | Pembrokeshire | Sir Benfro | Cardigan WwTW | 591 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216463 | 245943 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3ED | SA433ED | sa43 3ed | sa433ed | Pembrokeshire | Sir Benfro | Cardigan WwTW | 616 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216422 | 245993 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EE | SA433EE | sa43 3ee | sa433ee | Pembrokeshire | Sir Benfro | Cardigan WwTW | 631 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216405 | 245998 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EF | SA433EF | sa43 3ef | sa433ef | Pembrokeshire | Sir Benfro | Cardigan WwTW | 650 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216381 | 246020 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EH | SA433EH | sa43 3eh | sa433eh | Pembrokeshire | Sir Benfro | Cardigan WwTW | 670 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216373 | 245965 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EJ | SA433EJ | sa43 3ej | sa433ej | Pembrokeshire | Sir Benfro | Cardigan WwTW | 743 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216293 | 245987 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EN | SA433EN | sa43 3en | sa433en | Pembrokeshire | Sir Benfro | Cardigan WwTW | 814 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216234 | 245930 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EP | SA433EP | sa43 3ep | sa433ep | Pembrokeshire | Sir Benfro | Cardigan WwTW | 755 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216274 | 246022 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EQ | SA433EQ | sa43 3eq | sa433eq | Pembrokeshire | Sir Benfro | Cardigan WwTW | 780 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216253 | 245996 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3ER | SA433ER | sa43 3er | sa433er | Pembrokeshire | Sir Benfro | Cardigan WwTW | 760 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216267 | 246040 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3ES | SA433ES | sa43 3es | sa433es | Pembrokeshire | Sir Benfro | Cardigan WwTW | 718 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216303 | 246177 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3ET | SA433ET | sa43 3et | sa433et | Pembrokeshire | Sir Benfro | Cardigan WwTW | 622 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216399 | 246097 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EU | SA433EU | sa43 3eu | sa433eu | Pembrokeshire | Sir Benfro | Cardigan WwTW | 782 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216238 | 246153 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EW | SA433EW | sa43 3ew | sa433ew | Pembrokeshire | Sir Benfro | Cardigan WwTW | 804 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216216 | 246159 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EX | SA433EX | sa43 3ex | sa433ex | Pembrokeshire | Sir Benfro | Cardigan WwTW | 803 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216218 | 246105 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EY | SA433EY | sa43 3ey | sa433ey | Pembrokeshire | Sir Benfro | Cardigan WwTW | 786 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216268 | 246367 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3EZ | SA433EZ | sa43 3ez | sa433ez | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1198 | 1053 | 900to1200 | 2.11 | 1.54 | 1.13 | 19.63 | 10.47 | 11.57 | 217134 | 244947 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3GF | SA433GF | sa43 3gf | sa433gf | Pembrokeshire | Sir Benfro | Cardigan WwTW | 951 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 216320 | 246784 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HA | SA433HA | sa43 3ha | sa433ha | Pembrokeshire | Sir Benfro | Cardigan WwTW | 852 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216180 | 245997 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HB | SA433HB | sa43 3hb | sa433hb | Pembrokeshire | Sir Benfro | Cardigan WwTW | 865 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216186 | 245909 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HD | SA433HD | sa43 3hd | sa433hd | Pembrokeshire | Sir Benfro | Cardigan WwTW | 936 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216131 | 245848 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HE | SA433HE | sa43 3he | sa433he | Pembrokeshire | Sir Benfro | Cardigan WwTW | 907 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216155 | 245868 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HF | SA433HF | sa43 3hf | sa433hf | Pembrokeshire | Sir Benfro | Cardigan WwTW | 1023 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216076 | 245745 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HH | SA433HH | sa43 3hh | sa433hh | Pembrokeshire | Sir Benfro | Cardigan WwTW | 886 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216142 | 246022 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HP | SA433HP | sa43 3hp | sa433hp | Pembrokeshire | Sir Benfro | Cardigan WwTW | 379 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 216760 | 245864 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HR | SA433HR | sa43 3hr | sa433hr | Pembrokeshire | Sir Benfro | Cardigan WwTW | 475 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 216578 | 245967 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HS | SA433HS | sa43 3hs | sa433hs | Pembrokeshire | Sir Benfro | Cardigan WwTW | 331 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 216763 | 245932 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HT | SA433HT | sa43 3ht | sa433ht | Pembrokeshire | Sir Benfro | Cardigan WwTW | 503 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 216587 | 245885 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HU | SA433HU | sa43 3hu | sa433hu | Pembrokeshire | Sir Benfro | Cardigan WwTW | 579 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 216579 | 245765 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HX | SA433HX | sa43 3hx | sa433hx | Pembrokeshire | Sir Benfro | Cardigan WwTW | 488 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 216692 | 245779 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3HZ | SA433HZ | sa43 3hz | sa433hz | Pembrokeshire | Sir Benfro | Cardigan WwTW | 495 | 1019 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.99 | 10.13 | 11.2 | 216706 | 245757 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JA | SA433JA | sa43 3ja | sa433ja | Pembrokeshire | Sir Benfro | Cardigan WwTW | 715 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216490 | 245660 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JF | SA433JF | sa43 3jf | sa433jf | Pembrokeshire | Sir Benfro | Cardigan WwTW | 805 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216363 | 245674 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JG | SA433JG | sa43 3jg | sa433jg | Pembrokeshire | Sir Benfro | Cardigan WwTW | 863 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216238 | 245774 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JH | SA433JH | sa43 3jh | sa433jh | Pembrokeshire | Sir Benfro | Cardigan WwTW | 927 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 216350 | 245500 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JJ | SA433JJ | sa43 3jj | sa433jj | Pembrokeshire | Sir Benfro | Cardigan WwTW | 1143 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 216222 | 245321 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JL | SA433JL | sa43 3jl | sa433jl | Pembrokeshire | Sir Benfro | Cardigan WwTW | 1500 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 216067 | 244981 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JN | SA433JN | sa43 3jn | sa433jn | Pembrokeshire | Sir Benfro | Cardigan WwTW | 1689 | 1089 | 900to1200 | 2.18 | 1.59 | 1.17 | 20.3 | 10.83 | 11.96 | 215615 | 245203 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JP | SA433JP | sa43 3jp | sa433jp | Pembrokeshire | Sir Benfro | Cardigan WwTW | 2281 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 214740 | 246219 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JS | SA433JS | sa43 3js | sa433js | Pembrokeshire | Sir Benfro | Cardigan WwTW | 1885 | 1101 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.52 | 10.94 | 12.1 | 215165 | 245804 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JT | SA433JT | sa43 3jt | sa433jt | Pembrokeshire | Sir Benfro | Cardigan WwTW | 952 | 1058 | 900to1200 | 2.12 | 1.55 | 1.14 | 19.72 | 10.52 | 11.62 | 216071 | 246214 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JX | SA433JX | sa43 3jx | sa433jx | Pembrokeshire | Sir Benfro | Cardigan WwTW | 832 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 216275 | 246511 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JY | SA433JY | sa43 3jy | sa433jy | Pembrokeshire | Sir Benfro | Cardigan WwTW | 776 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 216346 | 246525 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3JZ | SA433JZ | sa43 3jz | sa433jz | Pembrokeshire | Sir Benfro | Cardigan WwTW | 857 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 216258 | 246533 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3LA | SA433LA | sa43 3la | sa433la | Pembrokeshire | Sir Benfro | Cardigan WwTW | 891 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 216268 | 246618 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3LD | SA433LD | sa43 3ld | sa433ld | Pembrokeshire | Sir Benfro | Cardigan WwTW | 887 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 216283 | 246634 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3LE | SA433LE | sa43 3le | sa433le | Pembrokeshire | Sir Benfro | Cardigan WwTW | 853 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 216320 | 246627 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3LF | SA433LF | sa43 3lf | sa433lf | Pembrokeshire | Sir Benfro | Cardigan WwTW | 818 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 216330 | 246580 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3LH | SA433LH | sa43 3lh | sa433lh | Pembrokeshire | Sir Benfro | Cardigan WwTW | 1062 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 216230 | 246850 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3LJ | SA433LJ | sa43 3lj | sa433lj | Pembrokeshire | Sir Benfro | Cardigan WwTW | 1015 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 216219 | 246764 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3LL | SA433LL | sa43 3ll | sa433ll | Pembrokeshire | Sir Benfro | Cardigan WwTW | 2204 | 952 | 900to1200 | 1.91 | 1.39 | 1.02 | 17.74 | 9.46 | 10.46 | 215795 | 247972 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3LN | SA433LN | sa43 3ln | sa433ln | Pembrokeshire | Sir Benfro | Cardigan WwTW | 2696 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 215484 | 248356 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3LR | SA433LR | sa43 3lr | sa433lr | Pembrokeshire | Sir Benfro | Cardigan WwTW | 2970 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 215203 | 248489 | Pembrokeshire Coast National Park LPA | PE | Afon Teifi/ River Teifi | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA43 3LS | SA433LS | sa43 3ls | sa433ls | Pembrokeshire | Sir Benfro | Cardigan WwTW | 3086 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 214608 | 248065 | Pembrokeshire Coast National Park LPA | PE | Afon Teifi/ River Teifi | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA43 3LT | SA433LT | sa43 3lt | sa433lt | Pembrokeshire | Sir Benfro | Cardigan WwTW | 3492 | 970 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.08 | 9.64 | 10.66 | 214195 | 248192 | Pembrokeshire Coast National Park LPA | PE | Afon Teifi/ River Teifi | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA43 3LW | SA433LW | sa43 3lw | sa433lw | Pembrokeshire | Sir Benfro | Cardigan WwTW | 2743 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 215109 | 248108 | Pembrokeshire Coast National Park LPA | PE | Afon Teifi/ River Teifi | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA43 3NA | SA433NA | sa43 3na | sa433na | Pembrokeshire | Sir Benfro | Cilgerran STW | 1694 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 217849 | 242783 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3NG | SA433NG | sa43 3ng | sa433ng | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1367 | 1020 | 900to1200 | 2.04 | 1.49 | 1.1 | 19.01 | 10.14 | 11.21 | 218204 | 245457 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3NH | SA433NH | sa43 3nh | sa433nh | Ceredigion | Sir Ceredigion | Cilgerran STW | 1932 | 1073 | 900to1200 | 2.15 | 1.57 | 1.15 | 20 | 10.67 | 11.79 | 217952 | 244423 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA43 3NJ | SA433NJ | sa43 3nj | sa433nj | Pembrokeshire | Sir Benfro | Cilgerran STW | 1764 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 217752 | 242884 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3NL | SA433NL | sa43 3nl | sa433nl | Pembrokeshire | Sir Benfro | Cilgerran STW | 1911 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 217599 | 242902 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3NN | SA433NN | sa43 3nn | sa433nn | Pembrokeshire | Sir Benfro | Cilgerran STW | 2627 | 1133 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.12 | 11.26 | 12.45 | 216872 | 242923 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3NP | SA433NP | sa43 3np | sa433np | Pembrokeshire | Sir Benfro | Cardigan WwTW | 2111 | 1137 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.19 | 11.3 | 12.49 | 216308 | 244153 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3NQ | SA433NQ | sa43 3nq | sa433nq | Pembrokeshire | Sir Benfro | Cilgerran STW | 1623 | 1090 | 900to1200 | 2.18 | 1.6 | 1.17 | 20.32 | 10.84 | 11.98 | 217906 | 242845 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3NR | SA433NR | sa43 3nr | sa433nr | Pembrokeshire | Sir Benfro | Cardigan WwTW | 2620 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 215252 | 244206 | Pembrokeshire LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3NT | SA433NT | sa43 3nt | sa433nt | Pembrokeshire | Sir Benfro | Cardigan WwTW | 3460 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 215579 | 242994 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3NU | SA433NU | sa43 3nu | sa433nu | Pembrokeshire | Sir Benfro | Cilgerran STW | 3971 | 1279 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.84 | 12.71 | 14.05 | 215607 | 242365 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 3NW | SA433NW | sa43 3nw | sa433nw | Pembrokeshire | Sir Benfro | Cardigan WwTW | 3462 | 1198 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.33 | 11.91 | 13.16 | 215722 | 242930 | Pembrokeshire LPA | PE | Afon Teifi/ River Teifi | Cyngor Sir Penfro | Pembrokeshire County Council
SA43 9AT | SA439AT | sa43 9at | sa439at | Ceredigion | Sir Ceredigion | Cardigan WwTW | 1014 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 218028 | 246034 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4AA | SA444AA | sa44 4aa | sa444aa | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 464 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 241448 | 240251 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4AE | SA444AE | sa44 4ae | sa444ae | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 466 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 241489 | 240090 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4AH | SA444AH | sa44 4ah | sa444ah | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 564 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 241353 | 240204 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4AJ | SA444AJ | sa44 4aj | sa444aj | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 791 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 241138 | 240118 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4AL | SA444AL | sa44 4al | sa444al | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 701 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 241220 | 240164 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4AP | SA444AP | sa44 4ap | sa444ap | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 823 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 241110 | 240095 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4BA | SA444BA | sa44 4ba | sa444ba | Ceredigion | Sir Ceredigion | Llandysul WwTW | 398 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 241526 | 240395 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4BD | SA444BD | sa44 4bd | sa444bd | Ceredigion | Sir Ceredigion | Llandysul WwTW | 345 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241657 | 240524 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4BH | SA444BH | sa44 4bh | sa444bh | Ceredigion | Sir Ceredigion | Llandysul WwTW | 363 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241629 | 240519 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4BJ | SA444BJ | sa44 4bj | sa444bj | Ceredigion | Sir Ceredigion | Llandysul WwTW | 363 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241697 | 240584 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4BL | SA444BL | sa44 4bl | sa444bl | Ceredigion | Sir Ceredigion | Llandysul WwTW | 410 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241586 | 240541 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4BN | SA444BN | sa44 4bn | sa444bn | Ceredigion | Sir Ceredigion | Llandysul WwTW | 365 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241700 | 240589 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4BS | SA444BS | sa44 4bs | sa444bs | Ceredigion | Sir Ceredigion | Llandysul WwTW | 377 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241681 | 240590 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4BU | SA444BU | sa44 4bu | sa444bu | Ceredigion | Sir Ceredigion | Llandysul WwTW | 397 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241704 | 240629 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4BX | SA444BX | sa44 4bx | sa444bx | Ceredigion | Sir Ceredigion | Llandysul WwTW | 433 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241697 | 240667 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4BY | SA444BY | sa44 4by | sa444by | Ceredigion | Sir Ceredigion | Llandysul WwTW | 415 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241655 | 240617 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4BZ | SA444BZ | sa44 4bz | sa444bz | Ceredigion | Sir Ceredigion | Llandysul WwTW | 475 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241565 | 240616 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DA | SA444DA | sa44 4da | sa444da | Ceredigion | Sir Ceredigion | Llandysul WwTW | 460 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241576 | 240606 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DB | SA444DB | sa44 4db | sa444db | Ceredigion | Sir Ceredigion | Llandysul WwTW | 463 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241677 | 240690 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DD | SA444DD | sa44 4dd | sa444dd | Ceredigion | Sir Ceredigion | Llandysul WwTW | 504 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241697 | 240747 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DE | SA444DE | sa44 4de | sa444de | Ceredigion | Sir Ceredigion | Llandysul WwTW | 450 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241713 | 240694 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DF | SA444DF | sa44 4df | sa444df | Ceredigion | Sir Ceredigion | Llandysul WwTW | 433 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241714 | 240676 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DG | SA444DG | sa44 4dg | sa444dg | Ceredigion | Sir Ceredigion | Llandysul WwTW | 485 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241759 | 240751 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DJ | SA444DJ | sa44 4dj | sa444dj | Ceredigion | Sir Ceredigion | Llandysul WwTW | 447 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241762 | 240712 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DL | SA444DL | sa44 4dl | sa444dl | Ceredigion | Sir Ceredigion | Llandysul WwTW | 484 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241777 | 240755 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DN | SA444DN | sa44 4dn | sa444dn | Ceredigion | Sir Ceredigion | Llandysul WwTW | 571 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241795 | 240849 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DP | SA444DP | sa44 4dp | sa444dp | Ceredigion | Sir Ceredigion | Llandysul WwTW | 543 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241811 | 240824 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DQ | SA444DQ | sa44 4dq | sa444dq | Ceredigion | Sir Ceredigion | Llandysul WwTW | 410 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241741 | 240663 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DR | SA444DR | sa44 4dr | sa444dr | Ceredigion | Sir Ceredigion | Llandysul WwTW | 712 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241852 | 241000 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DS | SA444DS | sa44 4ds | sa444ds | Ceredigion | Sir Ceredigion | Llandysul WwTW | 449 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241796 | 240724 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DT | SA444DT | sa44 4dt | sa444dt | Ceredigion | Sir Ceredigion | Llandysul WwTW | 763 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241746 | 241035 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DX | SA444DX | sa44 4dx | sa444dx | Ceredigion | Sir Ceredigion | Llandysul WwTW | 617 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241775 | 240892 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4DY | SA444DY | sa44 4dy | sa444dy | Ceredigion | Sir Ceredigion | Llandysul WwTW | 516 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241730 | 240774 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4EG | SA444EG | sa44 4eg | sa444eg | Ceredigion | Sir Ceredigion | Llandysul WwTW | 2018 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 242013 | 242305 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4EH | SA444EH | sa44 4eh | sa444eh | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3140 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 242360 | 243397 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4EJ | SA444EJ | sa44 4ej | sa444ej | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3594 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 242582 | 243820 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4EN | SA444EN | sa44 4en | sa444en | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 2382 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 243907 | 249130 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4EP | SA444EP | sa44 4ep | sa444ep | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 723 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 242652 | 250344 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4ER | SA444ER | sa44 4er | sa444er | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 122 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 242619 | 251033 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4ES | SA444ES | sa44 4es | sa444es | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 276 | 1418 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.43 | 14.1 | 15.58 | 242339 | 251275 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4ET | SA444ET | sa44 4et | sa444et | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 1162 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 241367 | 251315 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4EU | SA444EU | sa44 4eu | sa444eu | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 2274 | 1439 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.82 | 14.3 | 15.81 | 240231 | 250871 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4EW | SA444EW | sa44 4ew | sa444ew | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 1784 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 243458 | 249547 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4EX | SA444EX | sa44 4ex | sa444ex | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 2934 | 1439 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.82 | 14.3 | 15.81 | 239588 | 251420 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4EY | SA444EY | sa44 4ey | sa444ey | Ceredigion | Sir Ceredigion | Ffostrasol STW | 2781 | 1457 | 1200to1500 | 2.92 | 2.13 | 1.56 | 27.16 | 14.48 | 16.01 | 240117 | 249137 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HA | SA444HA | sa44 4ha | sa444ha | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 2428 | 1454 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.1 | 14.45 | 15.97 | 240347 | 249925 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HB | SA444HB | sa44 4hb | sa444hb | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 998 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241978 | 250198 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HD | SA444HD | sa44 4hd | sa444hd | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 1372 | 1427 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.6 | 14.19 | 15.68 | 243860 | 251211 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HE | SA444HE | sa44 4he | sa444he | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 1733 | 1445 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.93 | 14.36 | 15.88 | 244085 | 250354 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HG | SA444HG | sa44 4hg | sa444hg | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 2165 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 243958 | 249451 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HH | SA444HH | sa44 4hh | sa444hh | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 2141 | 1445 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.93 | 14.36 | 15.88 | 244377 | 250025 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HL | SA444HL | sa44 4hl | sa444hl | Ceredigion | Sir Ceredigion | Llandysul WwTW | 453 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241528 | 240534 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HN | SA444HN | sa44 4hn | sa444hn | Ceredigion | Sir Ceredigion | Llandysul WwTW | 538 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 241452 | 240572 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HP | SA444HP | sa44 4hp | sa444hp | Ceredigion | Sir Ceredigion | Llandysul WwTW | 721 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 241333 | 240723 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HR | SA444HR | sa44 4hr | sa444hr | Ceredigion | Sir Ceredigion | Llandysul WwTW | 962 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 241163 | 240896 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HS | SA444HS | sa44 4hs | sa444hs | Ceredigion | Sir Ceredigion | Llandysul WwTW | 821 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 241389 | 240924 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HT | SA444HT | sa44 4ht | sa444ht | Ceredigion | Sir Ceredigion | Llandysul WwTW | 872 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 241479 | 241048 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HU | SA444HU | sa44 4hu | sa444hu | Ceredigion | Sir Ceredigion | Llandysul WwTW | 1093 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 240872 | 240633 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HW | SA444HW | sa44 4hw | sa444hw | Ceredigion | Sir Ceredigion | Llandysul WwTW | 594 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 241418 | 240622 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HX | SA444HX | sa44 4hx | sa444hx | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 2020 | 1331 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.81 | 13.23 | 14.62 | 239841 | 240887 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HY | SA444HY | sa44 4hy | sa444hy | Ceredigion | Sir Ceredigion | Llandysul WwTW | 2616 | 1364 | 1200to1500 | 2.73 | 2 | 1.46 | 25.42 | 13.56 | 14.99 | 239870 | 241928 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4HZ | SA444HZ | sa44 4hz | sa444hz | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 2706 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 239425 | 241754 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JA | SA444JA | sa44 4ja | sa444ja | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 2706 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 239425 | 241754 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JB | SA444JB | sa44 4jb | sa444jb | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 3160 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 239016 | 242258 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JD | SA444JD | sa44 4jd | sa444jd | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 3276 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 238981 | 242375 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JE | SA444JE | sa44 4je | sa444je | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 3391 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 238963 | 242490 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JF | SA444JF | sa44 4jf | sa444jf | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 3375 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 239275 | 242454 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JG | SA444JG | sa44 4jg | sa444jg | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3300 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 239481 | 242523 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JH | SA444JH | sa44 4jh | sa444jh | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3178 | 1362 | 1200to1500 | 2.73 | 1.99 | 1.46 | 25.39 | 13.54 | 14.96 | 239693 | 242567 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JJ | SA444JJ | sa44 4jj | sa444jj | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3443 | 1362 | 1200to1500 | 2.73 | 1.99 | 1.46 | 25.39 | 13.54 | 14.96 | 239559 | 242805 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JL | SA444JL | sa44 4jl | sa444jl | Ceredigion | Sir Ceredigion | Llandysul WwTW | 2341 | 1364 | 1200to1500 | 2.73 | 2 | 1.46 | 25.42 | 13.56 | 14.99 | 240423 | 242098 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JN | SA444JN | sa44 4jn | sa444jn | Ceredigion | Sir Ceredigion | Llandysul WwTW | 1982 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 240945 | 242021 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JP | SA444JP | sa44 4jp | sa444jp | Ceredigion | Sir Ceredigion | Llandysul WwTW | 2755 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 240958 | 242875 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JQ | SA444JQ | sa44 4jq | sa444jq | Ceredigion | Sir Ceredigion | Llandysul WwTW | 961 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 241417 | 241115 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JR | SA444JR | sa44 4jr | sa444jr | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3740 | 1362 | 1200to1500 | 2.73 | 1.99 | 1.46 | 25.39 | 13.54 | 14.96 | 239985 | 243496 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JS | SA444JS | sa44 4js | sa444js | Ceredigion | Sir Ceredigion | Llandysul WwTW | 4059 | 1344 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.05 | 13.36 | 14.77 | 240271 | 244003 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JU | SA444JU | sa44 4ju | sa444ju | Ceredigion | Sir Ceredigion | Llandysul WwTW | 1077 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 241294 | 241173 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JW | SA444JW | sa44 4jw | sa444jw | Ceredigion | Sir Ceredigion | Llandysul WwTW | 1374 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 241129 | 241420 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4JX | SA444JX | sa44 4jx | sa444jx | Ceredigion | Sir Ceredigion | Llandysul WwTW | 1188 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 241248 | 241276 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LA | SA444LA | sa44 4la | sa444la | Ceredigion | Sir Ceredigion | Llandysul WwTW | 783 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241814 | 241067 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LB | SA444LB | sa44 4lb | sa444lb | Ceredigion | Sir Ceredigion | Llandysul WwTW | 1106 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241763 | 241386 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LD | SA444LD | sa44 4ld | sa444ld | Ceredigion | Sir Ceredigion | Llandysul WwTW | 1461 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 241593 | 241716 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LE | SA444LE | sa44 4le | sa444le | Ceredigion | Sir Ceredigion | Llandysul WwTW | 2145 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 241247 | 242330 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LF | SA444LF | sa44 4lf | sa444lf | Ceredigion | Sir Ceredigion | Llandysul WwTW | 2297 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 241172 | 242465 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LG | SA444LG | sa44 4lg | sa444lg | Ceredigion | Sir Ceredigion | Llandysul WwTW | 2357 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 241183 | 242532 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LH | SA444LH | sa44 4lh | sa444lh | Ceredigion | Sir Ceredigion | Llandysul WwTW | 2544 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 241165 | 242722 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LL | SA444LL | sa44 4ll | sa444ll | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3725 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 242177 | 244005 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LN | SA444LN | sa44 4ln | sa444ln | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3924 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 242460 | 244175 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LP | SA444LP | sa44 4lp | sa444lp | Ceredigion | Sir Ceredigion | Llandysul WwTW | 4001 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 242627 | 244226 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LQ | SA444LQ | sa44 4lq | sa444lq | Ceredigion | Sir Ceredigion | Llandysul WwTW | 2471 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 241153 | 242642 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LR | SA444LR | sa44 4lr | sa444lr | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3842 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 242489 | 244088 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LS | SA444LS | sa44 4ls | sa444ls | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3337 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 242843 | 243494 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LT | SA444LT | sa44 4lt | sa444lt | Ceredigion | Sir Ceredigion | Llandysul WwTW | 2780 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 242006 | 243068 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LU | SA444LU | sa44 4lu | sa444lu | Ceredigion | Sir Ceredigion | Llandysul WwTW | 4075 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 242525 | 244318 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LX | SA444LX | sa44 4lx | sa444lx | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3937 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 242395 | 244197 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LY | SA444LY | sa44 4ly | sa444ly | Ceredigion | Sir Ceredigion | Ffostrasol STW | 4348 | 1344 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.05 | 13.36 | 14.77 | 240984 | 244640 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4LZ | SA444LZ | sa44 4lz | sa444lz | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3803 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 240997 | 243981 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NA | SA444NA | sa44 4na | sa444na | Ceredigion | Sir Ceredigion | Ffostrasol STW | 4196 | 1344 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.05 | 13.36 | 14.77 | 240796 | 244663 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NB | SA444NB | sa44 4nb | sa444nb | Ceredigion | Sir Ceredigion | Ffostrasol STW | 4058 | 1344 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.05 | 13.36 | 14.77 | 240576 | 244641 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4ND | SA444ND | sa44 4nd | sa444nd | Ceredigion | Sir Ceredigion | Ffostrasol STW | 2818 | 1433 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.71 | 14.24 | 15.74 | 239471 | 245331 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NE | SA444NE | sa44 4ne | sa444ne | Ceredigion | Sir Ceredigion | Ffostrasol STW | 4424 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 241522 | 245210 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NG | SA444NG | sa44 4ng | sa444ng | Ceredigion | Sir Ceredigion | Ffostrasol STW | 4652 | 1416 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.39 | 14.08 | 15.56 | 242101 | 245829 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NH | SA444NH | sa44 4nh | sa444nh | Ceredigion | Sir Ceredigion | Ffostrasol STW | 4997 | 1392 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.94 | 13.84 | 15.29 | 242521 | 245965 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NJ | SA444NJ | sa44 4nj | sa444nj | Ceredigion | Sir Ceredigion | Ffostrasol STW | 4423 | 1416 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.39 | 14.08 | 15.56 | 241936 | 246033 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NL | SA444NL | sa44 4nl | sa444nl | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3237 | 1459 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.19 | 14.5 | 16.03 | 240859 | 246541 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NN | SA444NN | sa44 4nn | sa444nn | Ceredigion | Sir Ceredigion | Ffostrasol STW | 4010 | 1344 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.05 | 13.36 | 14.77 | 240697 | 244828 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NP | SA444NP | sa44 4np | sa444np | Ceredigion | Sir Ceredigion | Ffostrasol STW | 2123 | 1392 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.94 | 13.84 | 15.29 | 239081 | 245907 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NQ | SA444NQ | sa44 4nq | sa444nq | Ceredigion | Sir Ceredigion | Llandysul WwTW | 5026 | 1402 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.13 | 13.94 | 15.4 | 242661 | 245259 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NR | SA444NR | sa44 4nr | sa444nr | Ceredigion | Sir Ceredigion | Ffostrasol STW | 841 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 238632 | 247479 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NS | SA444NS | sa44 4ns | sa444ns | Ceredigion | Sir Ceredigion | Ffostrasol STW | 1257 | 1401 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.11 | 13.93 | 15.39 | 237971 | 246355 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NW | SA444NW | sa44 4nw | sa444nw | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3483 | 1344 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.05 | 13.36 | 14.77 | 240559 | 245475 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4NY | SA444NY | sa44 4ny | sa444ny | Ceredigion | Sir Ceredigion | Llandysul WwTW | 811 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241937 | 241100 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PA | SA444PA | sa44 4pa | sa444pa | Ceredigion | Sir Ceredigion | Llandysul WwTW | 1261 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 242092 | 241538 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PB | SA444PB | sa44 4pb | sa444pb | Ceredigion | Sir Ceredigion | Llandysul WwTW | 2065 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 242765 | 242169 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PD | SA444PD | sa44 4pd | sa444pd | Ceredigion | Sir Ceredigion | Llandysul WwTW | 1546 | 1312 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.45 | 13.04 | 14.41 | 243307 | 240952 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PF | SA444PF | sa44 4pf | sa444pf | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 2270 | 1389 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.89 | 13.81 | 15.26 | 244040 | 241866 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PG | SA444PG | sa44 4pg | sa444pg | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 2231 | 1389 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.89 | 13.81 | 15.26 | 244194 | 241936 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PH | SA444PH | sa44 4ph | sa444ph | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 2341 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 245108 | 242429 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PJ | SA444PJ | sa44 4pj | sa444pj | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 2010 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 244983 | 242065 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PL | SA444PL | sa44 4pl | sa444pl | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 2235 | 1386 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.83 | 13.78 | 15.23 | 245252 | 242342 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PN | SA444PN | sa44 4pn | sa444pn | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 2972 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 245973 | 243052 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PP | SA444PP | sa44 4pp | sa444pp | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 2786 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 245361 | 242903 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PQ | SA444PQ | sa44 4pq | sa444pq | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 2625 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 244762 | 242642 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PR | SA444PR | sa44 4pr | sa444pr | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 3535 | 1377 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.67 | 13.69 | 15.13 | 245955 | 243624 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PS | SA444PS | sa44 4ps | sa444ps | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 3784 | 1379 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.7 | 13.71 | 15.15 | 245226 | 243894 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PT | SA444PT | sa44 4pt | sa444pt | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 4055 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 246160 | 244731 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PU | SA444PU | sa44 4pu | sa444pu | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 4206 | 1379 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.7 | 13.71 | 15.15 | 244962 | 244292 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PX | SA444PX | sa44 4px | sa444px | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 4943 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 244482 | 244959 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4PY | SA444PY | sa44 4py | sa444py | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 5178 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 244568 | 245375 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QA | SA444QA | sa44 4qa | sa444qa | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 2862 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 246733 | 246203 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QB | SA444QB | sa44 4qb | sa444qb | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 5237 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 244353 | 245232 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QD | SA444QD | sa44 4qd | sa444qd | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 5225 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 244014 | 245132 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QE | SA444QE | sa44 4qe | sa444qe | Ceredigion | Sir Ceredigion | Llandysul WwTW | 4853 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 243719 | 244793 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QF | SA444QF | sa44 4qf | sa444qf | Ceredigion | Sir Ceredigion | Llandysul WwTW | 4911 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 243768 | 244835 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QJ | SA444QJ | sa44 4qj | sa444qj | Ceredigion | Sir Ceredigion | Llandysul WwTW | 292 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241712 | 240504 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QL | SA444QL | sa44 4ql | sa444ql | Ceredigion | Sir Ceredigion | Llandysul WwTW | 315 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241783 | 240578 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QN | SA444QN | sa44 4qn | sa444qn | Ceredigion | Sir Ceredigion | Llandysul WwTW | 398 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241751 | 240655 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QP | SA444QP | sa44 4qp | sa444qp | Ceredigion | Sir Ceredigion | Llandysul WwTW | 415 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241826 | 240696 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QS | SA444QS | sa44 4qs | sa444qs | Ceredigion | Sir Ceredigion | Llandysul WwTW | 468 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241864 | 240756 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QT | SA444QT | sa44 4qt | sa444qt | Ceredigion | Sir Ceredigion | Llandysul WwTW | 506 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241878 | 240795 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QU | SA444QU | sa44 4qu | sa444qu | Ceredigion | Sir Ceredigion | Llandysul WwTW | 530 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241870 | 240818 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QW | SA444QW | sa44 4qw | sa444qw | Ceredigion | Sir Ceredigion | Llandysul WwTW | 360 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241743 | 240609 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4QX | SA444QX | sa44 4qx | sa444qx | Ceredigion | Sir Ceredigion | Llandysul WwTW | 574 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 241892 | 240864 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4RA | SA444RA | sa44 4ra | sa444ra | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 1564 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 244007 | 240616 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4RB | SA444RB | sa44 4rb | sa444rb | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 1994 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 243867 | 241278 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4RD | SA444RD | sa44 4rd | sa444rd | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 2530 | 1389 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.89 | 13.81 | 15.26 | 244253 | 242327 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4RG | SA444RG | sa44 4rg | sa444rg | Ceredigion | Sir Ceredigion | Llanfihangel-Ar-Arth STW | 3819 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 243957 | 243617 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4RJ | SA444RJ | sa44 4rj | sa444rj | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 485 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 241582 | 239933 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4RL | SA444RL | sa44 4rl | sa444rl | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 463 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 242194 | 240655 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4RN | SA444RN | sa44 4rn | sa444rn | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 749 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 241918 | 239541 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4RP | SA444RP | sa44 4rp | sa444rp | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 1002 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 240955 | 239986 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4RR | SA444RR | sa44 4rr | sa444rr | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 1226 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 240806 | 239757 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4RS | SA444RS | sa44 4rs | sa444rs | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 899 | 1439 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.82 | 14.3 | 15.81 | 241511 | 239485 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4RT | SA444RT | sa44 4rt | sa444rt | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 1787 | 1447 | 1200to1500 | 2.9 | 2.12 | 1.55 | 26.97 | 14.38 | 15.9 | 242625 | 238652 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4RU | SA444RU | sa44 4ru | sa444ru | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 2015 | 1487 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.72 | 14.78 | 16.34 | 242107 | 238285 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4RW | SA444RW | sa44 4rw | sa444rw | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 1120 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 240862 | 239894 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4RX | SA444RX | sa44 4rx | sa444rx | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 1497 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 240504 | 239775 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4RY | SA444RY | sa44 4ry | sa444ry | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 2325 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 240924 | 237957 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4RZ | SA444RZ | sa44 4rz | sa444rz | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 2594 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 240944 | 237504 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4SA | SA444SA | sa44 4sa | sa444sa | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 3690 | 1652 | Over1500 | 3.31 | 2.42 | 1.77 | 30.79 | 16.42 | 18.15 | 240633 | 235843 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4SB | SA444SB | sa44 4sb | sa444sb | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 3409 | 1652 | Over1500 | 3.31 | 2.42 | 1.77 | 30.79 | 16.42 | 18.15 | 241267 | 235784 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4SD | SA444SD | sa44 4sd | sa444sd | Carmarthenshire | Sir Gaerfyrddin | Pencader STW | 4162 | 1755 | Over1500 | 3.51 | 2.57 | 1.88 | 32.71 | 17.45 | 19.28 | 240826 | 234747 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4SE | SA444SE | sa44 4se | sa444se | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 4394 | 1796 | Over1500 | 3.59 | 2.63 | 1.93 | 33.47 | 17.85 | 19.73 | 240862 | 234035 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4SF | SA444SF | sa44 4sf | sa444sf | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 1309 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 240751 | 239682 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 4SH | SA444SH | sa44 4sh | sa444sh | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3109 | 1396 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26.02 | 13.88 | 15.34 | 238264 | 244526 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4SJ | SA444SJ | sa44 4sj | sa444sj | Ceredigion | Sir Ceredigion | Ffostrasol STW | 2951 | 1396 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26.02 | 13.88 | 15.34 | 238264 | 244686 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4SL | SA444SL | sa44 4sl | sa444sl | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3321 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 238274 | 244313 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4SN | SA444SN | sa44 4sn | sa444sn | Ceredigion | Sir Ceredigion | Ffostrasol STW | 4253 | 1439 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.82 | 14.3 | 15.81 | 238973 | 243512 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4SP | SA444SP | sa44 4sp | sa444sp | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 3998 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 238386 | 243065 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4SR | SA444SR | sa44 4sr | sa444sr | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3594 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 237918 | 244008 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4SS | SA444SS | sa44 4ss | sa444ss | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3112 | 1396 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26.02 | 13.88 | 15.34 | 238440 | 244555 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4ST | SA444ST | sa44 4st | sa444st | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3239 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 238177 | 244383 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4SU | SA444SU | sa44 4su | sa444su | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3278 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 237876 | 244323 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4SX | SA444SX | sa44 4sx | sa444sx | Ceredigion | Sir Ceredigion | Ffostrasol STW | 2125 | 1396 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26.02 | 13.88 | 15.34 | 238122 | 245500 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4SY | SA444SY | sa44 4sy | sa444sy | Ceredigion | Sir Ceredigion | Ffostrasol STW | 515 | 1429 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.63 | 14.2 | 15.7 | 237288 | 247543 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4SZ | SA444SZ | sa44 4sz | sa444sz | Ceredigion | Sir Ceredigion | Ffostrasol STW | 502 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 237316 | 247466 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TA | SA444TA | sa44 4ta | sa444ta | Ceredigion | Sir Ceredigion | Ffostrasol STW | 547 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 237804 | 247053 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TB | SA444TB | sa44 4tb | sa444tb | Ceredigion | Sir Ceredigion | Ffostrasol STW | 733 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 237092 | 247411 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TD | SA444TD | sa44 4td | sa444td | Ceredigion | Sir Ceredigion | Ffostrasol STW | 588 | 1429 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.63 | 14.2 | 15.7 | 237313 | 247929 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TE | SA444TE | sa44 4te | sa444te | Ceredigion | Sir Ceredigion | Ffostrasol STW | 411 | 1429 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.63 | 14.2 | 15.7 | 237498 | 247879 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TF | SA444TF | sa44 4tf | sa444tf | Ceredigion | Sir Ceredigion | Ffostrasol STW | 409 | 1367 | 1200to1500 | 2.74 | 2 | 1.47 | 25.48 | 13.59 | 15.02 | 237618 | 247966 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TH | SA444TH | sa44 4th | sa444th | Ceredigion | Sir Ceredigion | Ffostrasol STW | 1327 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 238360 | 248803 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TJ | SA444TJ | sa44 4tj | sa444tj | Ceredigion | Sir Ceredigion | Ffostrasol STW | 1483 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 237977 | 249072 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TL | SA444TL | sa44 4tl | sa444tl | Ceredigion | Sir Ceredigion | Ffostrasol STW | 2533 | 1459 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.19 | 14.5 | 16.03 | 238551 | 250019 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TN | SA444TN | sa44 4tn | sa444tn | Ceredigion | Sir Ceredigion | Ffostrasol STW | 1939 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 238300 | 249473 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TP | SA444TP | sa44 4tp | sa444tp | Ceredigion | Sir Ceredigion | Ffostrasol STW | 2726 | 1457 | 1200to1500 | 2.92 | 2.13 | 1.56 | 27.16 | 14.48 | 16.01 | 239775 | 249479 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TQ | SA444TQ | sa44 4tq | sa444tq | Ceredigion | Sir Ceredigion | Ffostrasol STW | 749 | 1367 | 1200to1500 | 2.74 | 2 | 1.47 | 25.48 | 13.59 | 15.02 | 237776 | 248349 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TR | SA444TR | sa44 4tr | sa444tr | Ceredigion | Sir Ceredigion | Ffostrasol STW | 1483 | 1403 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.15 | 13.95 | 15.41 | 239127 | 248262 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TU | SA444TU | sa44 4tu | sa444tu | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 4961 | 1402 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.13 | 13.94 | 15.4 | 243899 | 246291 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TX | SA444TX | sa44 4tx | sa444tx | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 4635 | 1442 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.88 | 14.33 | 15.84 | 243943 | 246646 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TY | SA444TY | sa44 4ty | sa444ty | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 3934 | 1442 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.88 | 14.33 | 15.84 | 243966 | 247401 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4TZ | SA444TZ | sa44 4tz | sa444tz | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 3043 | 1422 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.5 | 14.14 | 15.62 | 243971 | 248388 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UA | SA444UA | sa44 4ua | sa444ua | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 2962 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 244591 | 248955 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UB | SA444UB | sa44 4ub | sa444ub | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 5307 | 1402 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.13 | 13.94 | 15.4 | 244281 | 245902 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UD | SA444UD | sa44 4ud | sa444ud | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 5372 | 1402 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.13 | 13.94 | 15.4 | 244296 | 245588 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UE | SA444UE | sa44 4ue | sa444ue | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3727 | 1445 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.93 | 14.36 | 15.88 | 245725 | 246988 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UG | SA444UG | sa44 4ug | sa444ug | Ceredigion | Sir Ceredigion | Gorsgoch STW | 2751 | 1416 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.39 | 14.08 | 15.56 | 246665 | 248113 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UL | SA444UL | sa44 4ul | sa444ul | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 5033 | 1402 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.13 | 13.94 | 15.4 | 243815 | 246193 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UN | SA444UN | sa44 4un | sa444un | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 5267 | 1392 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.94 | 13.84 | 15.29 | 243366 | 245856 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UP | SA444UP | sa44 4up | sa444up | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 4760 | 1402 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.13 | 13.94 | 15.4 | 243513 | 246400 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UR | SA444UR | sa44 4ur | sa444ur | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 4246 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 242749 | 246812 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UT | SA444UT | sa44 4ut | sa444ut | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 3898 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 241972 | 247188 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UU | SA444UU | sa44 4uu | sa444uu | Ceredigion | Sir Ceredigion | Ffostrasol STW | 2807 | 1416 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.39 | 14.08 | 15.56 | 240539 | 248213 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UX | SA444UX | sa44 4ux | sa444ux | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 2554 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 241297 | 248796 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4UY | SA444UY | sa44 4uy | sa444uy | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 2458 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 242507 | 248592 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4WH | SA444WH | sa44 4wh | sa444wh | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3300 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 239481 | 242523 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4XA | SA444XA | sa44 4xa | sa444xa | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 335 | 1418 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.43 | 14.1 | 15.58 | 242473 | 251384 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4XB | SA444XB | sa44 4xb | sa444xb | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 283 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 242779 | 251080 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4XD | SA444XD | sa44 4xd | sa444xd | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 1035 | 1428 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.62 | 14.2 | 15.69 | 243285 | 251722 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4XE | SA444XE | sa44 4xe | sa444xe | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 2091 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 243844 | 252650 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4XF | SA444XF | sa44 4xf | sa444xf | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 2578 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 243346 | 253484 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4XG | SA444XG | sa44 4xg | sa444xg | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 1996 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 242972 | 252989 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4XH | SA444XH | sa44 4xh | sa444xh | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 2185 | 1402 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.13 | 13.94 | 15.4 | 241743 | 253100 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4XN | SA444XN | sa44 4xn | sa444xn | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 835 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 241991 | 251713 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4XP | SA444XP | sa44 4xp | sa444xp | Ceredigion | Sir Ceredigion | Talgarreg WwTW | 1695 | 1442 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.88 | 14.33 | 15.84 | 241122 | 252040 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 4YR | SA444YR | sa44 4yr | sa444yr | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3300 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 239481 | 242523 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5AA | SA445AA | sa44 5aa | sa445aa | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1717 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 240230 | 238015 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AB | SA445AB | sa44 5ab | sa445ab | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 3208 | 1652 | Over1500 | 3.31 | 2.42 | 1.77 | 30.79 | 16.42 | 18.15 | 240514 | 236328 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AD | SA445AD | sa44 5ad | sa445ad | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 4092 | 1713 | Over1500 | 3.43 | 2.51 | 1.84 | 31.93 | 17.03 | 18.82 | 239164 | 234601 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AE | SA445AE | sa44 5ae | sa445ae | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 4035 | 1713 | Over1500 | 3.43 | 2.51 | 1.84 | 31.93 | 17.03 | 18.82 | 239219 | 235078 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AF | SA445AF | sa44 5af | sa445af | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 3800 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 238415 | 235331 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AG | SA445AG | sa44 5ag | sa445ag | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 3725 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 238329 | 235419 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AH | SA445AH | sa44 5ah | sa445ah | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 3122 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 239320 | 236007 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AJ | SA445AJ | sa44 5aj | sa445aj | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1910 | 1431 | 1200to1500 | 2.86 | 2.1 | 1.54 | 26.67 | 14.22 | 15.72 | 239181 | 237211 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AL | SA445AL | sa44 5al | sa445al | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1422 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 235597 | 238847 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AN | SA445AN | sa44 5an | sa445an | Ceredigion | Sir Ceredigion | Henllan STW | 256 | 1289 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.02 | 12.81 | 14.16 | 235575 | 240118 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5AP | SA445AP | sa44 5ap | sa445ap | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 922 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 240994 | 240189 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AR | SA445AR | sa44 5ar | sa445ar | Carmarthenshire | Sir Gaerfyrddin | Llandysul WwTW | 1432 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 240498 | 240055 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AS | SA445AS | sa44 5as | sa445as | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1297 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 239952 | 239858 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AT | SA445AT | sa44 5at | sa445at | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 245 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 238973 | 238866 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AU | SA445AU | sa44 5au | sa445au | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 553 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 238795 | 238557 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AX | SA445AX | sa44 5ax | sa445ax | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 532 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 238690 | 238611 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AY | SA445AY | sa44 5ay | sa445ay | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 736 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 238371 | 238588 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5AZ | SA445AZ | sa44 5az | sa445az | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1206 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 237715 | 239321 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5BA | SA445BA | sa44 5ba | sa445ba | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1416 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 237754 | 238269 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5BB | SA445BB | sa44 5bb | sa445bb | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 647 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 238313 | 238829 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5BD | SA445BD | sa44 5bd | sa445bd | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 389 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 238555 | 238920 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5BE | SA445BE | sa44 5be | sa445be | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 652 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 238441 | 239563 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5BH | SA445BH | sa44 5bh | sa445bh | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 1519 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 238227 | 240462 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5BJ | SA445BJ | sa44 5bj | sa445bj | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 1872 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 237637 | 240482 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5BL | SA445BL | sa44 5bl | sa445bl | Ceredigion | Sir Ceredigion | Henllan STW | 2212 | 1295 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.14 | 12.87 | 14.23 | 237484 | 240846 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5BN | SA445BN | sa44 5bn | sa445bn | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 2499 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 238393 | 241547 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5BP | SA445BP | sa44 5bp | sa445bp | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 1887 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 239057 | 240980 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5BQ | SA445BQ | sa44 5bq | sa445bq | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 758 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 238513 | 239752 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5BS | SA445BS | sa44 5bs | sa445bs | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 1456 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 239257 | 240511 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5BW | SA445BW | sa44 5bw | sa445bw | Ceredigion | Sir Ceredigion | Pentrecwrt STW | 2448 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 239058 | 241543 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5DA | SA445DA | sa44 5da | sa445da | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 632 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 239392 | 238704 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DB | SA445DB | sa44 5db | sa445db | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 850 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 239102 | 238274 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DD | SA445DD | sa44 5dd | sa445dd | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1070 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 239449 | 238182 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DE | SA445DE | sa44 5de | sa445de | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1710 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 239720 | 237600 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DF | SA445DF | sa44 5df | sa445df | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 582 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 238741 | 238540 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DG | SA445DG | sa44 5dg | sa445dg | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 538 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 238887 | 238562 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DJ | SA445DJ | sa44 5dj | sa445dj | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 613 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 238781 | 238499 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DL | SA445DL | sa44 5dl | sa445dl | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 709 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 238684 | 238425 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DP | SA445DP | sa44 5dp | sa445dp | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1445 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 238246 | 237812 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DR | SA445DR | sa44 5dr | sa445dr | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1703 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 237625 | 237971 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DS | SA445DS | sa44 5ds | sa445ds | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1846 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 237368 | 238071 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DT | SA445DT | sa44 5dt | sa445dt | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1974 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 237121 | 238245 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DU | SA445DU | sa44 5du | sa445du | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2355 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 236647 | 238279 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DW | SA445DW | sa44 5dw | sa445dw | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1634 | 1431 | 1200to1500 | 2.86 | 2.1 | 1.54 | 26.67 | 14.22 | 15.72 | 238590 | 237496 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DX | SA445DX | sa44 5dx | sa445dx | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2322 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 236631 | 238308 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DY | SA445DY | sa44 5dy | sa445dy | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1826 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 237561 | 237858 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5DZ | SA445DZ | sa44 5dz | sa445dz | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1993 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 237678 | 237526 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EA | SA445EA | sa44 5ea | sa445ea | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 2269 | 1492 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.81 | 14.83 | 16.39 | 238074 | 236987 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EB | SA445EB | sa44 5eb | sa445eb | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 2498 | 1492 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.81 | 14.83 | 16.39 | 237869 | 236825 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5ED | SA445ED | sa44 5ed | sa445ed | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 2906 | 1513 | Over1500 | 3.03 | 2.22 | 1.62 | 28.2 | 15.04 | 16.62 | 237853 | 236389 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EE | SA445EE | sa44 5ee | sa445ee | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 3421 | 1513 | Over1500 | 3.03 | 2.22 | 1.62 | 28.2 | 15.04 | 16.62 | 237837 | 235849 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EF | SA445EF | sa44 5ef | sa445ef | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 3662 | 1513 | Over1500 | 3.03 | 2.22 | 1.62 | 28.2 | 15.04 | 16.62 | 237964 | 235560 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EG | SA445EG | sa44 5eg | sa445eg | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 3762 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 237948 | 235461 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EH | SA445EH | sa44 5eh | sa445eh | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 2960 | 1513 | Over1500 | 3.03 | 2.22 | 1.62 | 28.2 | 15.04 | 16.62 | 237681 | 236403 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EJ | SA445EJ | sa44 5ej | sa445ej | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 2833 | 1494 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.85 | 14.85 | 16.41 | 237082 | 236927 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EL | SA445EL | sa44 5el | sa445el | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 2381 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 237123 | 237516 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EN | SA445EN | sa44 5en | sa445en | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1814 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 237305 | 238236 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EP | SA445EP | sa44 5ep | sa445ep | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1535 | 1372 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.57 | 13.64 | 15.07 | 237371 | 239229 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EQ | SA445EQ | sa44 5eq | sa445eq | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 4054 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 237983 | 235151 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5ES | SA445ES | sa44 5es | sa445es | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1270 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 237635 | 239211 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5ET | SA445ET | sa44 5et | sa445et | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1563 | 1372 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.57 | 13.64 | 15.07 | 237362 | 239378 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EU | SA445EU | sa44 5eu | sa445eu | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1602 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 237354 | 239518 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EW | SA445EW | sa44 5ew | sa445ew | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1640 | 1372 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.57 | 13.64 | 15.07 | 237298 | 238749 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EX | SA445EX | sa44 5ex | sa445ex | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1683 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 237281 | 239560 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EY | SA445EY | sa44 5ey | sa445ey | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1235 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 236579 | 240082 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5EZ | SA445EZ | sa44 5ez | sa445ez | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 773 | 1289 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.02 | 12.81 | 14.16 | 236080 | 239979 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5FA | SA445FA | sa44 5fa | sa445fa | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 1701 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 237265 | 239567 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HA | SA445HA | sa44 5ha | sa445ha | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1204 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 236552 | 240118 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HB | SA445HB | sa44 5hb | sa445hb | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 2784 | 1513 | Over1500 | 3.03 | 2.22 | 1.62 | 28.2 | 15.04 | 16.62 | 238443 | 236354 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HD | SA445HD | sa44 5hd | sa445hd | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 3630 | 1513 | Over1500 | 3.03 | 2.22 | 1.62 | 28.2 | 15.04 | 16.62 | 238150 | 235549 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HE | SA445HE | sa44 5he | sa445he | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 3900 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 237787 | 235363 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HF | SA445HF | sa44 5hf | sa445hf | Carmarthenshire | Sir Gaerfyrddin | Pentrecwrt STW | 4126 | 1643 | Over1500 | 3.29 | 2.41 | 1.76 | 30.62 | 16.33 | 18.05 | 237115 | 235381 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HG | SA445HG | sa44 5hg | sa445hg | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 3543 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 235181 | 236710 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HL | SA445HL | sa44 5hl | sa445hl | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2246 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 235607 | 238016 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HN | SA445HN | sa44 5hn | sa445hn | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2270 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 235524 | 237984 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HR | SA445HR | sa44 5hr | sa445hr | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2924 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 235095 | 237336 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HS | SA445HS | sa44 5hs | sa445hs | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 3258 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 235047 | 237005 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HT | SA445HT | sa44 5ht | sa445ht | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 3505 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 234922 | 236770 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HU | SA445HU | sa44 5hu | sa445hu | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 3657 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 234993 | 236609 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HW | SA445HW | sa44 5hw | sa445hw | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2600 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 235335 | 237648 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HX | SA445HX | sa44 5hx | sa445hx | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 3970 | 1586 | Over1500 | 3.17 | 2.32 | 1.7 | 29.56 | 15.77 | 17.43 | 234780 | 236320 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5HY | SA445HY | sa44 5hy | sa445hy | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 4805 | 1720 | Over1500 | 3.44 | 2.52 | 1.85 | 32.06 | 17.1 | 18.9 | 235023 | 235455 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5JA | SA445JA | sa44 5ja | sa445ja | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 4647 | 1541 | Over1500 | 3.08 | 2.26 | 1.66 | 28.72 | 15.32 | 16.93 | 235687 | 235613 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5JB | SA445JB | sa44 5jb | sa445jb | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 4291 | 1586 | Over1500 | 3.17 | 2.32 | 1.7 | 29.56 | 15.77 | 17.43 | 235458 | 235959 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5JD | SA445JD | sa44 5jd | sa445jd | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 3989 | 1586 | Over1500 | 3.17 | 2.32 | 1.7 | 29.56 | 15.77 | 17.43 | 235046 | 236271 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5JE | SA445JE | sa44 5je | sa445je | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 4135 | 1541 | Over1500 | 3.08 | 2.26 | 1.66 | 28.72 | 15.32 | 16.93 | 235703 | 236128 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5JF | SA445JF | sa44 5jf | sa445jf | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 3448 | 1458 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.17 | 14.49 | 16.02 | 235530 | 236805 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5JJ | SA445JJ | sa44 5jj | sa445jj | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 2471 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 235699 | 242735 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5JL | SA445JL | sa44 5jl | sa445jl | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2658 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 235372 | 244773 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5JP | SA445JP | sa44 5jp | sa445jp | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2229 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 236013 | 245595 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5JR | SA445JR | sa44 5jr | sa445jr | Ceredigion | Sir Ceredigion | Ffostrasol STW | 1793 | 1342 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.01 | 13.34 | 14.74 | 236284 | 246642 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5JS | SA445JS | sa44 5js | sa445js | Ceredigion | Sir Ceredigion | Ffostrasol STW | 1456 | 1342 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.01 | 13.34 | 14.74 | 236414 | 247153 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5JT | SA445JT | sa44 5jt | sa445jt | Ceredigion | Sir Ceredigion | Ffostrasol STW | 1446 | 1377 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.67 | 13.69 | 15.13 | 237258 | 246260 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5JU | SA445JU | sa44 5ju | sa445ju | Ceredigion | Sir Ceredigion | Ffostrasol STW | 1205 | 1401 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.11 | 13.93 | 15.39 | 237857 | 246396 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5JX | SA445JX | sa44 5jx | sa445jx | Ceredigion | Sir Ceredigion | Ffostrasol STW | 1328 | 1401 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.11 | 13.93 | 15.39 | 237948 | 246280 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5JY | SA445JY | sa44 5jy | sa445jy | Ceredigion | Sir Ceredigion | Ffostrasol STW | 2016 | 1401 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.11 | 13.93 | 15.39 | 237508 | 245605 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5JZ | SA445JZ | sa44 5jz | sa445jz | Ceredigion | Sir Ceredigion | Ffostrasol STW | 1458 | 1401 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.11 | 13.93 | 15.39 | 237952 | 246150 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LA | SA445LA | sa44 5la | sa445la | Ceredigion | Sir Ceredigion | Ffostrasol STW | 2909 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 237411 | 244717 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LB | SA445LB | sa44 5lb | sa445lb | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3145 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 236917 | 244582 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LD | SA445LD | sa44 5ld | sa445ld | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3115 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 236815 | 244645 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LE | SA445LE | sa44 5le | sa445le | Ceredigion | Sir Ceredigion | Ffostrasol STW | 2174 | 1377 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.67 | 13.69 | 15.13 | 236896 | 245623 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LH | SA445LH | sa44 5lh | sa445lh | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2301 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 235400 | 245159 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LJ | SA445LJ | sa44 5lj | sa445lj | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2721 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 234377 | 244602 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LL | SA445LL | sa44 5ll | sa445ll | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 3412 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 234861 | 243670 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LN | SA445LN | sa44 5ln | sa445ln | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2562 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 235599 | 244957 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LP | SA445LP | sa44 5lp | sa445lp | Ceredigion | Sir Ceredigion | Ffostrasol STW | 2888 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 236411 | 245068 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LQ | SA445LQ | sa44 5lq | sa445lq | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2456 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 235380 | 244987 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LR | SA445LR | sa44 5lr | sa445lr | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3234 | 1301 | 1200to1500 | 2.6 | 1.91 | 1.4 | 24.25 | 12.93 | 14.29 | 236167 | 244489 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LS | SA445LS | sa44 5ls | sa445ls | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2845 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 235815 | 244744 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LT | SA445LT | sa44 5lt | sa445lt | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3358 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 235161 | 244004 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LU | SA445LU | sa44 5lu | sa445lu | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3075 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 235497 | 244375 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LX | SA445LX | sa44 5lx | sa445lx | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3629 | 1301 | 1200to1500 | 2.6 | 1.91 | 1.4 | 24.25 | 12.93 | 14.29 | 235908 | 243932 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LY | SA445LY | sa44 5ly | sa445ly | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 3004 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 235540 | 243288 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5LZ | SA445LZ | sa44 5lz | sa445lz | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 2926 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 235987 | 243143 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NA | SA445NA | sa44 5na | sa445na | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3654 | 1301 | 1200to1500 | 2.6 | 1.91 | 1.4 | 24.25 | 12.93 | 14.29 | 236463 | 244174 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NB | SA445NB | sa44 5nb | sa445nb | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3668 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 236693 | 244103 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5ND | SA445ND | sa44 5nd | sa445nd | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3177 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 236722 | 244612 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NG | SA445NG | sa44 5ng | sa445ng | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 2252 | 1338 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.94 | 13.3 | 14.7 | 236894 | 241917 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NH | SA445NH | sa44 5nh | sa445nh | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 1759 | 1295 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.14 | 12.87 | 14.23 | 236637 | 241474 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NJ | SA445NJ | sa44 5nj | sa445nj | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 1720 | 1295 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.14 | 12.87 | 14.23 | 236881 | 241047 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NL | SA445NL | sa44 5nl | sa445nl | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 2001 | 1338 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.94 | 13.3 | 14.7 | 236637 | 241811 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NN | SA445NN | sa44 5nn | sa445nn | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 1982 | 1338 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.94 | 13.3 | 14.7 | 236568 | 241843 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NP | SA445NP | sa44 5np | sa445np | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 1506 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 235563 | 241780 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NQ | SA445NQ | sa44 5nq | sa445nq | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 1323 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 235748 | 241548 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NR | SA445NR | sa44 5nr | sa445nr | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 2576 | 1338 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.94 | 13.3 | 14.7 | 237231 | 242036 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NS | SA445NS | sa44 5ns | sa445ns | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 3168 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 237916 | 242129 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NT | SA445NT | sa44 5nt | sa445nt | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 2635 | 1338 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.94 | 13.3 | 14.7 | 237182 | 242171 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NU | SA445NU | sa44 5nu | sa445nu | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 3137 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 237583 | 242480 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NW | SA445NW | sa44 5nw | sa445nw | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 1751 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 236304 | 241750 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NX | SA445NX | sa44 5nx | sa445nx | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 2835 | 1338 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.94 | 13.3 | 14.7 | 237125 | 242490 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NY | SA445NY | sa44 5ny | sa445ny | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 2838 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 237018 | 242577 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5NZ | SA445NZ | sa44 5nz | sa445nz | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 3114 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 237009 | 242917 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PE | SA445PE | sa44 5pe | sa445pe | Ceredigion | Sir Ceredigion | Rhydlewis STW | 202 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 234742 | 247452 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PF | SA445PF | sa44 5pf | sa445pf | Ceredigion | Sir Ceredigion | Rhydlewis STW | 396 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 234798 | 247653 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PG | SA445PG | sa44 5pg | sa445pg | Ceredigion | Sir Ceredigion | Rhydlewis STW | 366 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 234740 | 247650 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PH | SA445PH | sa44 5ph | sa445ph | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1721 | 1262 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.52 | 12.54 | 13.87 | 234582 | 249035 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PJ | SA445PJ | sa44 5pj | sa445pj | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2051 | 1262 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.52 | 12.54 | 13.87 | 235100 | 249301 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PL | SA445PL | sa44 5pl | sa445pl | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2772 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 235732 | 249841 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PN | SA445PN | sa44 5pn | sa445pn | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2512 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 234224 | 249798 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PP | SA445PP | sa44 5pp | sa445pp | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3245 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 235102 | 250519 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PQ | SA445PQ | sa44 5pq | sa445pq | Ceredigion | Sir Ceredigion | Rhydlewis STW | 986 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 234732 | 248290 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PR | SA445PR | sa44 5pr | sa445pr | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3350 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 234412 | 250659 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PS | SA445PS | sa44 5ps | sa445ps | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3592 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 234309 | 250894 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PT | SA445PT | sa44 5pt | sa445pt | Ceredigion | Sir Ceredigion | Rhydlewis STW | 4868 | 1270 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.67 | 12.62 | 13.95 | 233933 | 252137 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5PU | SA445PU | sa44 5pu | sa445pu | Ceredigion | Sir Ceredigion | Rhydlewis STW | 5026 | 1270 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.67 | 12.62 | 13.95 | 233775 | 252273 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QB | SA445QB | sa44 5qb | sa445qb | Ceredigion | Sir Ceredigion | Rhydlewis STW | 522 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 234971 | 246953 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QD | SA445QD | sa44 5qd | sa445qd | Ceredigion | Sir Ceredigion | Rhydlewis STW | 506 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 234682 | 246816 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QE | SA445QE | sa44 5qe | sa445qe | Ceredigion | Sir Ceredigion | Rhydlewis STW | 783 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 234510 | 246536 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QG | SA445QG | sa44 5qg | sa445qg | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1437 | 1312 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.45 | 13.04 | 14.41 | 234789 | 245890 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QH | SA445QH | sa44 5qh | sa445qh | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1719 | 1226 | 1200to1500 | 2.45 | 1.8 | 1.32 | 22.85 | 12.19 | 13.47 | 234399 | 245606 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QJ | SA445QJ | sa44 5qj | sa445qj | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1725 | 1140 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.25 | 11.33 | 12.53 | 233422 | 246049 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QN | SA445QN | sa44 5qn | sa445qn | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1465 | 1226 | 1200to1500 | 2.45 | 1.8 | 1.32 | 22.85 | 12.19 | 13.47 | 233543 | 246294 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QQ | SA445QQ | sa44 5qq | sa445qq | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1623 | 1312 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.45 | 13.04 | 14.41 | 234961 | 245733 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QR | SA445QR | sa44 5qr | sa445qr | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2202 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 232441 | 247775 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QS | SA445QS | sa44 5qs | sa445qs | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1514 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 233080 | 247323 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QT | SA445QT | sa44 5qt | sa445qt | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1408 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 233337 | 247949 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QU | SA445QU | sa44 5qu | sa445qu | Ceredigion | Sir Ceredigion | Rhydlewis STW | 928 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 233667 | 247343 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QX | SA445QX | sa44 5qx | sa445qx | Ceredigion | Sir Ceredigion | Rhydlewis STW | 700 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 233921 | 247120 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5QY | SA445QY | sa44 5qy | sa445qy | Ceredigion | Sir Ceredigion | Rhydlewis STW | 621 | 1197 | 900to1200 | 2.4 | 1.75 | 1.29 | 22.31 | 11.9 | 13.15 | 233998 | 247488 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5RE | SA445RE | sa44 5re | sa445re | Ceredigion | Sir Ceredigion | Rhydlewis STW | 143 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 234732 | 247278 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5RF | SA445RF | sa44 5rf | sa445rf | Ceredigion | Sir Ceredigion | Rhydlewis STW | 236 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 234688 | 247097 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5RG | SA445RG | sa44 5rg | sa445rg | Ceredigion | Sir Ceredigion | Rhydlewis STW | 335 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 234696 | 246995 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5RH | SA445RH | sa44 5rh | sa445rh | Ceredigion | Sir Ceredigion | Rhydlewis STW | 530 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 234511 | 246791 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5RJ | SA445RJ | sa44 5rj | sa445rj | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1851 | 1142 | 900to1200 | 2.29 | 1.67 | 1.23 | 21.29 | 11.35 | 12.55 | 232920 | 246524 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5RL | SA445RL | sa44 5rl | sa445rl | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2293 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 232334 | 246925 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5RN | SA445RN | sa44 5rn | sa445rn | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2340 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 232258 | 247172 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5RR | SA445RR | sa44 5rr | sa445rr | Ceredigion | Sir Ceredigion | Beulah WwTW | 2036 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 230826 | 247688 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5RS | SA445RS | sa44 5rs | sa445rs | Ceredigion | Sir Ceredigion | Beulah WwTW | 1922 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 230346 | 247876 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5RT | SA445RT | sa44 5rt | sa445rt | Ceredigion | Sir Ceredigion | Beulah WwTW | 2071 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 230915 | 247653 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5RW | SA445RW | sa44 5rw | sa445rw | Ceredigion | Sir Ceredigion | Beulah WwTW | 2603 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 231829 | 247281 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5RY | SA445RY | sa44 5ry | sa445ry | Ceredigion | Sir Ceredigion | Rhydlewis STW | 772 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 235064 | 247926 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5SA | SA445SA | sa44 5sa | sa445sa | Ceredigion | Sir Ceredigion | Rhydlewis STW | 757 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 235206 | 247760 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5SB | SA445SB | sa44 5sb | sa445sb | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1577 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 236120 | 247713 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5SD | SA445SD | sa44 5sd | sa445sd | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1326 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 235722 | 248011 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5SG | SA445SG | sa44 5sg | sa445sg | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1920 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 235615 | 248940 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5SH | SA445SH | sa44 5sh | sa445sh | Ceredigion | Sir Ceredigion | Rhydlewis STW | 688 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 235273 | 247206 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5SL | SA445SL | sa44 5sl | sa445sl | Ceredigion | Sir Ceredigion | Rhydlewis STW | 113 | 1251 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.32 | 12.44 | 13.74 | 234509 | 247388 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5SN | SA445SN | sa44 5sn | sa445sn | Ceredigion | Sir Ceredigion | Rhydlewis STW | 681 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 234014 | 247671 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5SP | SA445SP | sa44 5sp | sa445sp | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1956 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 233439 | 248892 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5SR | SA445SR | sa44 5sr | sa445sr | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3048 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 233083 | 249961 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5SS | SA445SS | sa44 5ss | sa445ss | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2314 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 233267 | 249210 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5ST | SA445ST | sa44 5st | sa445st | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2690 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 233615 | 249819 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5SW | SA445SW | sa44 5sw | sa445sw | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1877 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 233220 | 248592 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5SX | SA445SX | sa44 5sx | sa445sx | Ceredigion | Sir Ceredigion | Rhydlewis STW | 1190 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 234346 | 248478 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TD | SA445TD | sa44 5td | sa445td | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 468 | 1289 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.02 | 12.81 | 14.16 | 235723 | 240554 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TE | SA445TE | sa44 5te | sa445te | Ceredigion | Sir Ceredigion | Henllan STW | 193 | 1289 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.02 | 12.81 | 14.16 | 235546 | 240218 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TG | SA445TG | sa44 5tg | sa445tg | Carmarthenshire | Sir Gaerfyrddin | Drefach/Velindre WwTW | 584 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 234752 | 240283 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5TH | SA445TH | sa44 5th | sa445th | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 612 | 1289 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.02 | 12.81 | 14.16 | 235854 | 240617 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TJ | SA445TJ | sa44 5tj | sa445tj | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 737 | 1289 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.02 | 12.81 | 14.16 | 235967 | 240671 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TL | SA445TL | sa44 5tl | sa445tl | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 679 | 1289 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.02 | 12.81 | 14.16 | 235951 | 240578 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TN | SA445TN | sa44 5tn | sa445tn | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 960 | 1289 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.02 | 12.81 | 14.16 | 236218 | 240669 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TP | SA445TP | sa44 5tp | sa445tp | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 1045 | 1289 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.02 | 12.81 | 14.16 | 235524 | 241319 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TR | SA445TR | sa44 5tr | sa445tr | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 981 | 1248 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.26 | 12.41 | 13.71 | 235162 | 241256 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TS | SA445TS | sa44 5ts | sa445ts | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 1266 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 235252 | 241554 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TT | SA445TT | sa44 5tt | sa445tt | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 1917 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 234877 | 242152 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TU | SA445TU | sa44 5tu | sa445tu | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 2215 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 234004 | 242061 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TX | SA445TX | sa44 5tx | sa445tx | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 3432 | 1292 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.08 | 12.84 | 14.2 | 233642 | 243275 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5TY | SA445TY | sa44 5ty | sa445ty | Ceredigion | Sir Ceredigion | Drefach/Velindre WwTW | 3590 | 1275 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.76 | 12.67 | 14.01 | 234057 | 243645 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5UA | SA445UA | sa44 5ua | sa445ua | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2783 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 233781 | 244653 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5UB | SA445UB | sa44 5ub | sa445ub | Ceredigion | Sir Ceredigion | Adpar WwTW | 3882 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 233083 | 243708 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5UG | SA445UG | sa44 5ug | sa445ug | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1709 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 235404 | 238540 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UH | SA445UH | sa44 5uh | sa445uh | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1393 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 235448 | 238858 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UJ | SA445UJ | sa44 5uj | sa445uj | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1354 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 235519 | 238904 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UL | SA445UL | sa44 5ul | sa445ul | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1369 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 235497 | 238886 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UN | SA445UN | sa44 5un | sa445un | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1381 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 235853 | 238960 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UP | SA445UP | sa44 5up | sa445up | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1158 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 235521 | 239102 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UQ | SA445UQ | sa44 5uq | sa445uq | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1592 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 235487 | 238662 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UR | SA445UR | sa44 5ur | sa445ur | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1086 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 235602 | 239191 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UT | SA445UT | sa44 5ut | sa445ut | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 880 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 235651 | 239419 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UU | SA445UU | sa44 5uu | sa445uu | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1671 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 235534 | 238587 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UW | SA445UW | sa44 5uw | sa445uw | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1876 | 1372 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.57 | 13.64 | 15.07 | 236938 | 239242 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UX | SA445UX | sa44 5ux | sa445ux | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1588 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 235593 | 238678 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UY | SA445UY | sa44 5uy | sa445uy | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1922 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 235597 | 238341 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5UZ | SA445UZ | sa44 5uz | sa445uz | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1505 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 235634 | 238769 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5WX | SA445WX | sa44 5wx | sa445wx | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3300 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 239481 | 242523 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 5XA | SA445XA | sa44 5xa | sa445xa | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2211 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 235740 | 238071 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XB | SA445XB | sa44 5xb | sa445xb | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2324 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 235988 | 238012 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XD | SA445XD | sa44 5xd | sa445xd | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2589 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 236221 | 237808 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XE | SA445XE | sa44 5xe | sa445xe | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2735 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 236313 | 237686 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XG | SA445XG | sa44 5xg | sa445xg | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1999 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 235439 | 238251 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XH | SA445XH | sa44 5xh | sa445xh | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1741 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 235222 | 238512 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XJ | SA445XJ | sa44 5xj | sa445xj | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2212 | 1474 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.47 | 14.65 | 16.19 | 234331 | 238287 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XL | SA445XL | sa44 5xl | sa445xl | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2611 | 1474 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.47 | 14.65 | 16.19 | 234042 | 237991 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XN | SA445XN | sa44 5xn | sa445xn | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2909 | 1474 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.47 | 14.65 | 16.19 | 233869 | 237747 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XP | SA445XP | sa44 5xp | sa445xp | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 2580 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 234692 | 237755 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XR | SA445XR | sa44 5xr | sa445xr | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 3558 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 234191 | 236886 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XS | SA445XS | sa44 5xs | sa445xs | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 3786 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 234446 | 236573 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XT | SA445XT | sa44 5xt | sa445xt | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 4696 | 1615 | Over1500 | 3.23 | 2.37 | 1.73 | 30.1 | 16.05 | 17.74 | 233996 | 235733 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XU | SA445XU | sa44 5xu | sa445xu | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 4192 | 1615 | Over1500 | 3.23 | 2.37 | 1.73 | 30.1 | 16.05 | 17.74 | 233731 | 236384 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5XW | SA445XW | sa44 5xw | sa445xw | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 3016 | 1474 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.47 | 14.65 | 16.19 | 233515 | 237859 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5YA | SA445YA | sa44 5ya | sa445ya | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1753 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 235326 | 238495 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5YB | SA445YB | sa44 5yb | sa445yb | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1668 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 235209 | 238587 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5YD | SA445YD | sa44 5yd | sa445yd | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1575 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 234998 | 238714 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5YF | SA445YF | sa44 5yf | sa445yf | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1407 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 234908 | 238914 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5YG | SA445YG | sa44 5yg | sa445yg | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1294 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 234626 | 239179 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5YH | SA445YH | sa44 5yh | sa445yh | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1374 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 234449 | 239215 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5YL | SA445YL | sa44 5yl | sa445yl | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1865 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 233795 | 239227 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5YN | SA445YN | sa44 5yn | sa445yn | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1341 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 235121 | 238928 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5YQ | SA445YQ | sa44 5yq | sa445yq | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1367 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 234467 | 239209 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5YW | SA445YW | sa44 5yw | sa445yw | Carmarthenshire | Sir Gaerfyrddin | Henllan STW | 1187 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 235117 | 239085 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA44 5ZA | SA445ZA | sa44 5za | sa445za | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3300 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 239481 | 242523 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6AA | SA446AA | sa44 6aa | sa446aa | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2759 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 232976 | 249549 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6AB | SA446AB | sa44 6ab | sa446ab | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3241 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 232855 | 250049 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6BD | SA446BD | sa44 6bd | sa446bd | Ceredigion | Sir Ceredigion | Rhydlewis STW | 4874 | 1146 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.36 | 11.39 | 12.59 | 231158 | 250770 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6BQ | SA446BQ | sa44 6bq | sa446bq | Ceredigion | Sir Ceredigion | Rhydlewis STW | 4805 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 231515 | 251002 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6DX | SA446DX | sa44 6dx | sa446dx | Ceredigion | Sir Ceredigion | Rhydlewis STW | 4300 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 233283 | 251409 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6DY | SA446DY | sa44 6dy | sa446dy | Ceredigion | Sir Ceredigion | Rhydlewis STW | 4230 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 233661 | 251440 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6EB | SA446EB | sa44 6eb | sa446eb | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3251 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 232581 | 249866 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6EG | SA446EG | sa44 6eg | sa446eg | Ceredigion | Sir Ceredigion | Rhydlewis STW | 5082 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 233489 | 252274 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6EH | SA446EH | sa44 6eh | sa446eh | Ceredigion | Sir Ceredigion | Rhydlewis STW | 5528 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 233491 | 252731 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6EQ | SA446EQ | sa44 6eq | sa446eq | Ceredigion | Sir Ceredigion | Rhydlewis STW | 5217 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 233483 | 252411 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6HR | SA446HR | sa44 6hr | sa446hr | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3899 | 1354 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.24 | 13.46 | 14.88 | 235625 | 251074 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6HT | SA446HT | sa44 6ht | sa446ht | Ceredigion | Sir Ceredigion | Ffostrasol STW | 4225 | 1348 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.12 | 13.4 | 14.81 | 236801 | 251705 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6HU | SA446HU | sa44 6hu | sa446hu | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3766 | 1354 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.24 | 13.46 | 14.88 | 236488 | 251130 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6HX | SA446HX | sa44 6hx | sa446hx | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3873 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 237145 | 251417 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6JW | SA446JW | sa44 6jw | sa446jw | Ceredigion | Sir Ceredigion | Ffostrasol STW | 3972 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 238264 | 251545 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6NX | SA446NX | sa44 6nx | sa446nx | Ceredigion | Sir Ceredigion | Beulah WwTW | 2849 | 1171 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.83 | 11.64 | 12.87 | 231087 | 248512 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6NY | SA446NY | sa44 6ny | sa446ny | Ceredigion | Sir Ceredigion | Beulah WwTW | 3121 | 1171 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.83 | 11.64 | 12.87 | 230556 | 249089 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6NZ | SA446NZ | sa44 6nz | sa446nz | Ceredigion | Sir Ceredigion | Beulah WwTW | 2173 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 230246 | 248193 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6PA | SA446PA | sa44 6pa | sa446pa | Ceredigion | Sir Ceredigion | Beulah WwTW | 2248 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 229754 | 248391 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6PB | SA446PB | sa44 6pb | sa446pb | Ceredigion | Sir Ceredigion | Beulah WwTW | 3436 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 229941 | 249565 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6PD | SA446PD | sa44 6pd | sa446pd | Ceredigion | Sir Ceredigion | Beulah WwTW | 3144 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 230023 | 249257 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6PE | SA446PE | sa44 6pe | sa446pe | Ceredigion | Sir Ceredigion | Beulah WwTW | 3789 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 230876 | 249682 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6PG | SA446PG | sa44 6pg | sa446pg | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3766 | 1171 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.83 | 11.64 | 12.87 | 231497 | 249456 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6PH | SA446PH | sa44 6ph | sa446ph | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3160 | 1226 | 1200to1500 | 2.45 | 1.8 | 1.32 | 22.85 | 12.19 | 13.47 | 231916 | 248991 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6PJ | SA446PJ | sa44 6pj | sa446pj | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3274 | 1226 | 1200to1500 | 2.45 | 1.8 | 1.32 | 22.85 | 12.19 | 13.47 | 231629 | 248702 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6PL | SA446PL | sa44 6pl | sa446pl | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2853 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 231949 | 248382 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6PN | SA446PN | sa44 6pn | sa446pn | Ceredigion | Sir Ceredigion | Rhydlewis STW | 3007 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 231781 | 248375 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6PP | SA446PP | sa44 6pp | sa446pp | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2816 | 1226 | 1200to1500 | 2.45 | 1.8 | 1.32 | 22.85 | 12.19 | 13.47 | 232178 | 248760 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6PR | SA446PR | sa44 6pr | sa446pr | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2209 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 232653 | 248368 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6PS | SA446PS | sa44 6ps | sa446ps | Ceredigion | Sir Ceredigion | Rhydlewis STW | 2140 | 1218 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.7 | 12.11 | 13.38 | 232640 | 248187 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6QQ | SA446QQ | sa44 6qq | sa446qq | Ceredigion | Sir Ceredigion | Rhydlewis STW | 4853 | 1146 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.36 | 11.39 | 12.59 | 231240 | 250821 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6QT | SA446QT | sa44 6qt | sa446qt | Ceredigion | Sir Ceredigion | Beulah WwTW | 4869 | 1146 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.36 | 11.39 | 12.59 | 230962 | 250798 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6QU | SA446QU | sa44 6qu | sa446qu | Ceredigion | Sir Ceredigion | Beulah WwTW | 4331 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 230189 | 250432 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6QX | SA446QX | sa44 6qx | sa446qx | Ceredigion | Sir Ceredigion | Beulah WwTW | 4198 | 1164 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.7 | 11.57 | 12.79 | 229898 | 250337 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6RE | SA446RE | sa44 6re | sa446re | Ceredigion | Sir Ceredigion | Rhydlewis STW | 4279 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 232128 | 250811 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 6RF | SA446RF | sa44 6rf | sa446rf | Ceredigion | Sir Ceredigion | Rhydlewis STW | 4437 | 1189 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.16 | 11.82 | 13.06 | 231664 | 250646 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 9AB | SA449AB | sa44 9ab | sa449ab | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3300 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 239481 | 242523 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 9AW | SA449AW | sa44 9aw | sa449aw | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3300 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 239481 | 242523 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 9AY | SA449AY | sa44 9ay | sa449ay | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3300 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 239481 | 242523 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 9BB | SA449BB | sa44 9bb | sa449bb | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3300 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 239481 | 242523 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA44 9BD | SA449BD | sa44 9bd | sa449bd | Ceredigion | Sir Ceredigion | Llandysul WwTW | 3300 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 239481 | 242523 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AA | SA487AA | sa48 7aa | sa487aa | Ceredigion | Sir Ceredigion | Lampeter STW | 686 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257856 | 247988 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AB | SA487AB | sa48 7ab | sa487ab | Ceredigion | Sir Ceredigion | Lampeter STW | 624 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257945 | 247878 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AD | SA487AD | sa48 7ad | sa487ad | Ceredigion | Sir Ceredigion | Cribyn WwTW | 760 | 1277 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.8 | 12.69 | 14.03 | 252258 | 250904 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AE | SA487AE | sa48 7ae | sa487ae | Ceredigion | Sir Ceredigion | Lampeter STW | 628 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257740 | 247958 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AF | SA487AF | sa48 7af | sa487af | Ceredigion | Sir Ceredigion | Lampeter STW | 568 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258015 | 247757 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AG | SA487AG | sa48 7ag | sa487ag | Ceredigion | Sir Ceredigion | Lampeter STW | 559 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257961 | 247790 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AJ | SA487AJ | sa48 7aj | sa487aj | Ceredigion | Sir Ceredigion | Lampeter STW | 528 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257820 | 247833 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AL | SA487AL | sa48 7al | sa487al | Ceredigion | Sir Ceredigion | Lampeter STW | 600 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257812 | 247912 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AN | SA487AN | sa48 7an | sa487an | Ceredigion | Sir Ceredigion | Lampeter STW | 577 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257717 | 247910 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AP | SA487AP | sa48 7ap | sa487ap | Ceredigion | Sir Ceredigion | Lampeter STW | 510 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257715 | 247843 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AQ | SA487AQ | sa48 7aq | sa487aq | Ceredigion | Sir Ceredigion | Lampeter STW | 489 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257787 | 247803 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AR | SA487AR | sa48 7ar | sa487ar | Ceredigion | Sir Ceredigion | Lampeter STW | 627 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257770 | 247951 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AS | SA487AS | sa48 7as | sa487as | Ceredigion | Sir Ceredigion | Lampeter STW | 656 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257729 | 247988 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AT | SA487AT | sa48 7at | sa487at | Ceredigion | Sir Ceredigion | Lampeter STW | 705 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257769 | 248031 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7AU | SA487AU | sa48 7au | sa487au | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3678 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 253128 | 247108 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BA | SA487BA | sa48 7ba | sa487ba | Ceredigion | Sir Ceredigion | Lampeter STW | 758 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257725 | 248092 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BB | SA487BB | sa48 7bb | sa487bb | Ceredigion | Sir Ceredigion | Lampeter STW | 783 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257669 | 248122 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BG | SA487BG | sa48 7bg | sa487bg | Ceredigion | Sir Ceredigion | Lampeter STW | 769 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257599 | 248108 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BH | SA487BH | sa48 7bh | sa487bh | Ceredigion | Sir Ceredigion | Lampeter STW | 831 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257521 | 248164 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BJ | SA487BJ | sa48 7bj | sa487bj | Ceredigion | Sir Ceredigion | Lampeter STW | 858 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 257457 | 248180 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BN | SA487BN | sa48 7bn | sa487bn | Ceredigion | Sir Ceredigion | Lampeter STW | 941 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 257363 | 248242 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BQ | SA487BQ | sa48 7bq | sa487bq | Ceredigion | Sir Ceredigion | Lampeter STW | 754 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257681 | 248092 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BR | SA487BR | sa48 7br | sa487br | Ceredigion | Sir Ceredigion | Lampeter STW | 947 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257625 | 248287 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BS | SA487BS | sa48 7bs | sa487bs | Ceredigion | Sir Ceredigion | Lampeter STW | 917 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 257438 | 248237 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BT | SA487BT | sa48 7bt | sa487bt | Ceredigion | Sir Ceredigion | Lampeter STW | 882 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257551 | 248218 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BU | SA487BU | sa48 7bu | sa487bu | Ceredigion | Sir Ceredigion | Lampeter STW | 788 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257514 | 248119 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BX | SA487BX | sa48 7bx | sa487bx | Ceredigion | Sir Ceredigion | Lampeter STW | 667 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257577 | 248005 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BY | SA487BY | sa48 7by | sa487by | Ceredigion | Sir Ceredigion | Lampeter STW | 473 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257586 | 247811 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7BZ | SA487BZ | sa48 7bz | sa487bz | Ceredigion | Sir Ceredigion | Lampeter STW | 545 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257561 | 247881 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DA | SA487DA | sa48 7da | sa487da | Ceredigion | Sir Ceredigion | Lampeter STW | 458 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 257499 | 247779 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DB | SA487DB | sa48 7db | sa487db | Ceredigion | Sir Ceredigion | Lampeter STW | 770 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257532 | 248104 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DD | SA487DD | sa48 7dd | sa487dd | Ceredigion | Sir Ceredigion | Lampeter STW | 689 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257618 | 248029 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DF | SA487DF | sa48 7df | sa487df | Ceredigion | Sir Ceredigion | Lampeter STW | 622 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257685 | 247959 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DG | SA487DG | sa48 7dg | sa487dg | Ceredigion | Sir Ceredigion | Lampeter STW | 674 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257670 | 248013 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DL | SA487DL | sa48 7dl | sa487dl | Ceredigion | Sir Ceredigion | Lampeter STW | 815 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257676 | 248154 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DP | SA487DP | sa48 7dp | sa487dp | Ceredigion | Sir Ceredigion | Lampeter STW | 886 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257763 | 248216 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DQ | SA487DQ | sa48 7dq | sa487dq | Ceredigion | Sir Ceredigion | Lampeter STW | 704 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257718 | 248038 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DR | SA487DR | sa48 7dr | sa487dr | Ceredigion | Sir Ceredigion | Lampeter STW | 856 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257744 | 248188 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DS | SA487DS | sa48 7ds | sa487ds | Ceredigion | Sir Ceredigion | Lampeter STW | 826 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257703 | 248163 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DT | SA487DT | sa48 7dt | sa487dt | Ceredigion | Sir Ceredigion | Lampeter STW | 801 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257786 | 248126 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DU | SA487DU | sa48 7du | sa487du | Ceredigion | Sir Ceredigion | Lampeter STW | 791 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257781 | 248116 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DW | SA487DW | sa48 7dw | sa487dw | Ceredigion | Sir Ceredigion | Lampeter STW | 852 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257770 | 248180 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DX | SA487DX | sa48 7dx | sa487dx | Ceredigion | Sir Ceredigion | Lampeter STW | 791 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257758 | 248120 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DY | SA487DY | sa48 7dy | sa487dy | Ceredigion | Sir Ceredigion | Lampeter STW | 902 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257820 | 248222 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7DZ | SA487DZ | sa48 7dz | sa487dz | Ceredigion | Sir Ceredigion | Lampeter STW | 1152 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258050 | 248412 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7EA | SA487EA | sa48 7ea | sa487ea | Ceredigion | Sir Ceredigion | Lampeter STW | 1263 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258160 | 248486 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7ED | SA487ED | sa48 7ed | sa487ed | Ceredigion | Sir Ceredigion | Lampeter STW | 907 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257916 | 248201 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7EE | SA487EE | sa48 7ee | sa487ee | Ceredigion | Sir Ceredigion | Lampeter STW | 976 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257742 | 248309 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7EF | SA487EF | sa48 7ef | sa487ef | Ceredigion | Sir Ceredigion | Lampeter STW | 895 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257655 | 248235 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7EG | SA487EG | sa48 7eg | sa487eg | Ceredigion | Sir Ceredigion | Lampeter STW | 905 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257595 | 248244 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7EH | SA487EH | sa48 7eh | sa487eh | Ceredigion | Sir Ceredigion | Lampeter STW | 949 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 257456 | 248273 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7EJ | SA487EJ | sa48 7ej | sa487ej | Ceredigion | Sir Ceredigion | Lampeter STW | 1061 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 257364 | 248367 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7EL | SA487EL | sa48 7el | sa487el | Ceredigion | Sir Ceredigion | Lampeter STW | 1022 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 257465 | 248348 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7EN | SA487EN | sa48 7en | sa487en | Ceredigion | Sir Ceredigion | Lampeter STW | 1031 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 257334 | 248327 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7EP | SA487EP | sa48 7ep | sa487ep | Ceredigion | Sir Ceredigion | Lampeter STW | 1201 | 1278 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.82 | 12.7 | 14.04 | 257438 | 248525 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7EQ | SA487EQ | sa48 7eq | sa487eq | Ceredigion | Sir Ceredigion | Lampeter STW | 1257 | 1278 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.82 | 12.7 | 14.04 | 257398 | 248575 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7ER | SA487ER | sa48 7er | sa487er | Ceredigion | Sir Ceredigion | Lampeter STW | 998 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257679 | 248337 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7ES | SA487ES | sa48 7es | sa487es | Ceredigion | Sir Ceredigion | Lampeter STW | 1051 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257631 | 248391 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7ET | SA487ET | sa48 7et | sa487et | Ceredigion | Sir Ceredigion | Lampeter STW | 1102 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257698 | 248440 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7EU | SA487EU | sa48 7eu | sa487eu | Ceredigion | Sir Ceredigion | Lampeter STW | 1201 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257676 | 248540 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7EY | SA487EY | sa48 7ey | sa487ey | Ceredigion | Sir Ceredigion | Lampeter STW | 1042 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257877 | 248352 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HB | SA487HB | sa48 7hb | sa487hb | Ceredigion | Sir Ceredigion | Lampeter STW | 1099 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258022 | 248366 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HD | SA487HD | sa48 7hd | sa487hd | Ceredigion | Sir Ceredigion | Lampeter STW | 760 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257767 | 248087 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HE | SA487HE | sa48 7he | sa487he | Ceredigion | Sir Ceredigion | Lampeter STW | 778 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257793 | 248101 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HF | SA487HF | sa48 7hf | sa487hf | Ceredigion | Sir Ceredigion | Lampeter STW | 754 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257783 | 248078 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HG | SA487HG | sa48 7hg | sa487hg | Ceredigion | Sir Ceredigion | Lampeter STW | 762 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257837 | 248073 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HH | SA487HH | sa48 7hh | sa487hh | Ceredigion | Sir Ceredigion | Lampeter STW | 1116 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257998 | 248393 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HP | SA487HP | sa48 7hp | sa487hp | Ceredigion | Sir Ceredigion | Lampeter STW | 1105 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258127 | 248327 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HR | SA487HR | sa48 7hr | sa487hr | Ceredigion | Sir Ceredigion | Lampeter STW | 957 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258084 | 248182 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HS | SA487HS | sa48 7hs | sa487hs | Ceredigion | Sir Ceredigion | Lampeter STW | 1300 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258014 | 248582 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HU | SA487HU | sa48 7hu | sa487hu | Ceredigion | Sir Ceredigion | Lampeter STW | 1393 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258067 | 248662 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HX | SA487HX | sa48 7hx | sa487hx | Ceredigion | Sir Ceredigion | Lampeter STW | 1151 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257966 | 248441 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HY | SA487HY | sa48 7hy | sa487hy | Ceredigion | Sir Ceredigion | Lampeter STW | 1234 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258034 | 248506 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7HZ | SA487HZ | sa48 7hz | sa487hz | Ceredigion | Sir Ceredigion | Lampeter STW | 1197 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257889 | 248508 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JA | SA487JA | sa48 7ja | sa487ja | Ceredigion | Sir Ceredigion | Lampeter STW | 1420 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257789 | 248751 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JB | SA487JB | sa48 7jb | sa487jb | Ceredigion | Sir Ceredigion | Lampeter STW | 1545 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257729 | 248882 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JD | SA487JD | sa48 7jd | sa487jd | Ceredigion | Sir Ceredigion | Lampeter STW | 1328 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257764 | 248661 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JE | SA487JE | sa48 7je | sa487je | Ceredigion | Sir Ceredigion | Lampeter STW | 1312 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257725 | 248648 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JL | SA487JL | sa48 7jl | sa487jl | Ceredigion | Sir Ceredigion | Lampeter STW | 992 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 257239 | 248251 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JN | SA487JN | sa48 7jn | sa487jn | Ceredigion | Sir Ceredigion | Lampeter STW | 1016 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 257063 | 248183 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JP | SA487JP | sa48 7jp | sa487jp | Ceredigion | Sir Ceredigion | Lampeter STW | 1371 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 256260 | 247399 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JR | SA487JR | sa48 7jr | sa487jr | Ceredigion | Sir Ceredigion | Lampeter STW | 2576 | 1294 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.12 | 12.86 | 14.22 | 255057 | 247235 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JS | SA487JS | sa48 7js | sa487js | Ceredigion | Sir Ceredigion | Lampeter STW | 3579 | 1282 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.89 | 12.74 | 14.09 | 254052 | 247358 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JT | SA487JT | sa48 7jt | sa487jt | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3937 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 253385 | 247214 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JU | SA487JU | sa48 7ju | sa487ju | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3883 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 253332 | 247156 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JW | SA487JW | sa48 7jw | sa487jw | Ceredigion | Sir Ceredigion | Lampeter STW | 1122 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 257026 | 248285 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JX | SA487JX | sa48 7jx | sa487jx | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3879 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 253328 | 247031 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7JY | SA487JY | sa48 7jy | sa487jy | Ceredigion | Sir Ceredigion | Llanybydder WwTW | 3431 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 253049 | 246429 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LA | SA487LA | sa48 7la | sa487la | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3847 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 253291 | 247301 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LB | SA487LB | sa48 7lb | sa487lb | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3773 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 253206 | 247451 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LD | SA487LD | sa48 7ld | sa487ld | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3733 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 253164 | 247474 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LE | SA487LE | sa48 7le | sa487le | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3387 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 252763 | 247802 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LF | SA487LF | sa48 7lf | sa487lf | Ceredigion | Sir Ceredigion | Cribyn WwTW | 2027 | 1279 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.84 | 12.71 | 14.05 | 252097 | 249209 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LG | SA487LG | sa48 7lg | sa487lg | Ceredigion | Sir Ceredigion | Cribyn WwTW | 3521 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 253191 | 248048 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LH | SA487LH | sa48 7lh | sa487lh | Ceredigion | Sir Ceredigion | Lampeter STW | 3871 | 1282 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.89 | 12.74 | 14.09 | 253795 | 246820 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LJ | SA487LJ | sa48 7lj | sa487lj | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3411 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 252858 | 246974 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LL | SA487LL | sa48 7ll | sa487ll | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3699 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 253126 | 247505 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LN | SA487LN | sa48 7ln | sa487ln | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1445 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 250642 | 247917 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LP | SA487LP | sa48 7lp | sa487lp | Ceredigion | Sir Ceredigion | Cribyn WwTW | 2328 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 249855 | 249554 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LQ | SA487LQ | sa48 7lq | sa487lq | Ceredigion | Sir Ceredigion | Lampeter STW | 4054 | 1282 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.89 | 12.74 | 14.09 | 253588 | 247036 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LR | SA487LR | sa48 7lr | sa487lr | Ceredigion | Sir Ceredigion | Cribyn WwTW | 1818 | 1309 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.4 | 13.01 | 14.38 | 250577 | 249617 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LT | SA487LT | sa48 7lt | sa487lt | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 3750 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 253190 | 247368 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LU | SA487LU | sa48 7lu | sa487lu | Ceredigion | Sir Ceredigion | Cribyn WwTW | 816 | 1277 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.8 | 12.69 | 14.03 | 252303 | 250863 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LW | SA487LW | sa48 7lw | sa487lw | Ceredigion | Sir Ceredigion | Cwrtnewydd STW | 1637 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 250674 | 248187 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LX | SA487LX | sa48 7lx | sa487lx | Ceredigion | Sir Ceredigion | Lampeter STW | 1152 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258050 | 248412 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LY | SA487LY | sa48 7ly | sa487ly | Ceredigion | Sir Ceredigion | Cribyn WwTW | 2319 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 252529 | 249060 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7LZ | SA487LZ | sa48 7lz | sa487lz | Ceredigion | Sir Ceredigion | Cribyn WwTW | 1287 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 252310 | 250125 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NA | SA487NA | sa48 7na | sa487na | Ceredigion | Sir Ceredigion | Cribyn WwTW | 715 | 1277 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.8 | 12.69 | 14.03 | 252233 | 250975 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NB | SA487NB | sa48 7nb | sa487nb | Ceredigion | Sir Ceredigion | Cribyn WwTW | 613 | 1277 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.8 | 12.69 | 14.03 | 252154 | 251192 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7ND | SA487ND | sa48 7nd | sa487nd | Ceredigion | Sir Ceredigion | Cribyn WwTW | 286 | 1277 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.8 | 12.69 | 14.03 | 251827 | 251186 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NE | SA487NE | sa48 7ne | sa487ne | Ceredigion | Sir Ceredigion | Cribyn WwTW | 576 | 1277 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.8 | 12.69 | 14.03 | 252023 | 251475 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NF | SA487NF | sa48 7nf | sa487nf | Ceredigion | Sir Ceredigion | Cribyn WwTW | 691 | 1268 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.63 | 12.6 | 13.93 | 252054 | 251622 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NG | SA487NG | sa48 7ng | sa487ng | Ceredigion | Sir Ceredigion | Cribyn WwTW | 744 | 1268 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.63 | 12.6 | 13.93 | 252052 | 251700 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NH | SA487NH | sa48 7nh | sa487nh | Ceredigion | Sir Ceredigion | Cribyn WwTW | 1233 | 1268 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.63 | 12.6 | 13.93 | 252017 | 252296 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NL | SA487NL | sa48 7nl | sa487nl | Ceredigion | Sir Ceredigion | Cribyn WwTW | 2103 | 1302 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.27 | 12.94 | 14.3 | 251585 | 253260 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NP | SA487NP | sa48 7np | sa487np | Ceredigion | Sir Ceredigion | Cribyn WwTW | 1768 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 253227 | 251693 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NQ | SA487NQ | sa48 7nq | sa487nq | Ceredigion | Sir Ceredigion | Cribyn WwTW | 1849 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 252652 | 252636 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NR | SA487NR | sa48 7nr | sa487nr | Ceredigion | Sir Ceredigion | Cribyn WwTW | 1901 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 253441 | 251239 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NT | SA487NT | sa48 7nt | sa487nt | Ceredigion | Sir Ceredigion | Cribyn WwTW | 2886 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 253887 | 249476 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NU | SA487NU | sa48 7nu | sa487nu | Ceredigion | Sir Ceredigion | Lampeter STW | 3316 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 255142 | 249532 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NX | SA487NX | sa48 7nx | sa487nx | Ceredigion | Sir Ceredigion | Lampeter STW | 3619 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 254316 | 248794 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NY | SA487NY | sa48 7ny | sa487ny | Ceredigion | Sir Ceredigion | Cribyn WwTW | 3123 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 253481 | 248710 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7NZ | SA487NZ | sa48 7nz | sa487nz | Ceredigion | Sir Ceredigion | Cribyn WwTW | 729 | 1277 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.8 | 12.69 | 14.03 | 252209 | 250863 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7PA | SA487PA | sa48 7pa | sa487pa | Ceredigion | Sir Ceredigion | Lampeter STW | 1220 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 256704 | 248134 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7PB | SA487PB | sa48 7pb | sa487pb | Ceredigion | Sir Ceredigion | Cribyn WwTW | 626 | 1268 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.63 | 12.6 | 13.93 | 252059 | 251510 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7QH | SA487QH | sa48 7qh | sa487qh | Ceredigion | Sir Ceredigion | Cribyn WwTW | 770 | 1306 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.34 | 12.98 | 14.35 | 251029 | 251732 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7QJ | SA487QJ | sa48 7qj | sa487qj | Ceredigion | Sir Ceredigion | Cribyn WwTW | 1944 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 249994 | 252334 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7QL | SA487QL | sa48 7ql | sa487ql | Ceredigion | Sir Ceredigion | Cribyn WwTW | 3208 | 1312 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.45 | 13.04 | 14.41 | 249714 | 253794 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7QN | SA487QN | sa48 7qn | sa487qn | Ceredigion | Sir Ceredigion | Cribyn WwTW | 2693 | 1349 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.14 | 13.41 | 14.82 | 249486 | 252897 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7QW | SA487QW | sa48 7qw | sa487qw | Ceredigion | Sir Ceredigion | Gorsgoch STW | 2465 | 1349 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.14 | 13.41 | 14.82 | 249252 | 252529 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7RX | SA487RX | sa48 7rx | sa487rx | Ceredigion | Sir Ceredigion | Lampeter STW | 2310 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 256393 | 249291 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7RZ | SA487RZ | sa48 7rz | sa487rz | Ceredigion | Sir Ceredigion | Lampeter STW | 2666 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 256225 | 249605 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 7SB | SA487SB | sa48 7sb | sa487sb | Ceredigion | Sir Ceredigion | Lampeter STW | 1169 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 257048 | 248354 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AA | SA488AA | sa48 8aa | sa488aa | Ceredigion | Sir Ceredigion | Lampeter STW | 2257 | 1278 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.82 | 12.7 | 14.04 | 256609 | 249352 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AB | SA488AB | sa48 8ab | sa488ab | Ceredigion | Sir Ceredigion | Lampeter STW | 3622 | 1326 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.71 | 13.18 | 14.57 | 256180 | 250658 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AJ | SA488AJ | sa48 8aj | sa488aj | Ceredigion | Sir Ceredigion | Cellan WwTW | 3835 | 1341 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.99 | 13.33 | 14.73 | 256914 | 251194 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AL | SA488AL | sa48 8al | sa488al | Ceredigion | Sir Ceredigion | Lampeter STW | 1547 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257607 | 248887 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AN | SA488AN | sa48 8an | sa488an | Ceredigion | Sir Ceredigion | Lampeter STW | 1769 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257605 | 249109 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AP | SA488AP | sa48 8ap | sa488ap | Ceredigion | Sir Ceredigion | Lampeter STW | 3232 | 1341 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.99 | 13.33 | 14.73 | 257205 | 250543 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AR | SA488AR | sa48 8ar | sa488ar | Ceredigion | Sir Ceredigion | Cellan WwTW | 2929 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 257741 | 250801 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AS | SA488AS | sa48 8as | sa488as | Ceredigion | Sir Ceredigion | Cellan WwTW | 3457 | 1341 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.99 | 13.33 | 14.73 | 257286 | 251071 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AT | SA488AT | sa48 8at | sa488at | Ceredigion | Sir Ceredigion | Cellan WwTW | 3778 | 1341 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.99 | 13.33 | 14.73 | 256984 | 251198 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AU | SA488AU | sa48 8au | sa488au | Ceredigion | Sir Ceredigion | Llangybi STW | 3787 | 1341 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.99 | 13.33 | 14.73 | 257031 | 251458 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AW | SA488AW | sa48 8aw | sa488aw | Ceredigion | Sir Ceredigion | Lampeter STW | 1563 | 1278 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.82 | 12.7 | 14.04 | 257422 | 248889 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AX | SA488AX | sa48 8ax | sa488ax | Ceredigion | Sir Ceredigion | Lampeter STW | 4304 | 1326 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.71 | 13.18 | 14.57 | 256450 | 251478 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AY | SA488AY | sa48 8ay | sa488ay | Ceredigion | Sir Ceredigion | Cribyn WwTW | 3914 | 1288 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.01 | 12.8 | 14.15 | 255219 | 252499 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8AZ | SA488AZ | sa48 8az | sa488az | Ceredigion | Sir Ceredigion | Cribyn WwTW | 3786 | 1289 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.02 | 12.81 | 14.16 | 255056 | 252567 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8BA | SA488BA | sa48 8ba | sa488ba | Ceredigion | Sir Ceredigion | Cribyn WwTW | 3801 | 1289 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.02 | 12.81 | 14.16 | 254958 | 252823 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8BJ | SA488BJ | sa48 8bj | sa488bj | Ceredigion | Sir Ceredigion | Cribyn WwTW | 4376 | 1266 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.6 | 12.58 | 13.91 | 255172 | 253601 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8BL | SA488BL | sa48 8bl | sa488bl | Ceredigion | Sir Ceredigion | Cribyn WwTW | 4270 | 1289 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.02 | 12.81 | 14.16 | 255443 | 252894 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8BN | SA488BN | sa48 8bn | sa488bn | Ceredigion | Sir Ceredigion | Llangybi STW | 3791 | 1295 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.14 | 12.87 | 14.23 | 256714 | 253453 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8BS | SA488BS | sa48 8bs | sa488bs | Ceredigion | Sir Ceredigion | Lampeter STW | 1446 | 1278 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.82 | 12.7 | 14.04 | 257472 | 248777 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8DN | SA488DN | sa48 8dn | sa488dn | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 631 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 258165 | 247006 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8DR | SA488DR | sa48 8dr | sa488dr | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 664 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 258294 | 247321 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8DS | SA488DS | sa48 8ds | sa488ds | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 894 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 258155 | 246617 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8DT | SA488DT | sa48 8dt | sa488dt | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 540 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 258139 | 247161 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8DU | SA488DU | sa48 8du | sa488du | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 740 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 257573 | 246602 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8DX | SA488DX | sa48 8dx | sa488dx | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1998 | 1348 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.12 | 13.4 | 14.81 | 256220 | 245925 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8DY | SA488DY | sa48 8dy | sa488dy | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1727 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 256951 | 245752 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8DZ | SA488DZ | sa48 8dz | sa488dz | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1331 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 257770 | 246017 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EA | SA488EA | sa48 8ea | sa488ea | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 2354 | 1446 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.95 | 14.37 | 15.89 | 257199 | 245026 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EB | SA488EB | sa48 8eb | sa488eb | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 3098 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 255972 | 244723 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8ED | SA488ED | sa48 8ed | sa488ed | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 3564 | 1468 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.36 | 14.59 | 16.13 | 256844 | 243864 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EE | SA488EE | sa48 8ee | sa488ee | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 4137 | 1484 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.66 | 14.75 | 16.3 | 256157 | 243475 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EF | SA488EF | sa48 8ef | sa488ef | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 570 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 257932 | 246857 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EG | SA488EG | sa48 8eg | sa488eg | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 2696 | 1448 | 1200to1500 | 2.9 | 2.12 | 1.56 | 26.99 | 14.39 | 15.91 | 258204 | 244706 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EH | SA488EH | sa48 8eh | sa488eh | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1582 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 259061 | 246665 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EJ | SA488EJ | sa48 8ej | sa488ej | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1333 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 258904 | 246948 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EL | SA488EL | sa48 8el | sa488el | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 916 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 258528 | 247160 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EN | SA488EN | sa48 8en | sa488en | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1464 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 259085 | 247176 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EP | SA488EP | sa48 8ep | sa488ep | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1149 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 258720 | 246978 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8ER | SA488ER | sa48 8er | sa488er | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1684 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 259229 | 246814 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8ES | SA488ES | sa48 8es | sa488es | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1697 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 259160 | 246607 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8ET | SA488ET | sa48 8et | sa488et | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1505 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 258873 | 246492 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EU | SA488EU | sa48 8eu | sa488eu | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1864 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 258606 | 245752 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EW | SA488EW | sa48 8ew | sa488ew | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1264 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 258812 | 246892 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EX | SA488EX | sa48 8ex | sa488ex | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 2991 | 1471 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.42 | 14.62 | 16.16 | 259081 | 244725 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EY | SA488EY | sa48 8ey | sa488ey | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 3562 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 259564 | 244350 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HH | SA488HH | sa48 8hh | sa488hh | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 2807 | 1495 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.86 | 14.86 | 16.43 | 261018 | 245650 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HJ | SA488HJ | sa48 8hj | sa488hj | Ceredigion | Sir Ceredigion | Heol Timothy STW | 2730 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 262369 | 246756 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8HL | SA488HL | sa48 8hl | sa488hl | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 2777 | 1501 | Over1500 | 3 | 2.2 | 1.61 | 27.98 | 14.92 | 16.49 | 263251 | 247019 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HN | SA488HN | sa48 8hn | sa488hn | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 3152 | 1494 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.85 | 14.85 | 16.41 | 264050 | 247611 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HP | SA488HP | sa48 8hp | sa488hp | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1426 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 258968 | 246847 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HQ | SA488HQ | sa48 8hq | sa488hq | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 2404 | 1452 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.06 | 14.43 | 15.95 | 259545 | 245888 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HT | SA488HT | sa48 8ht | sa488ht | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 924 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 258553 | 247369 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HU | SA488HU | sa48 8hu | sa488hu | Ceredigion | Sir Ceredigion | Cellan WwTW | 780 | 1341 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.99 | 13.33 | 14.73 | 259753 | 248422 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8HW | SA488HW | sa48 8hw | sa488hw | Ceredigion | Sir Ceredigion | Farmers STW | 3623 | 1551 | Over1500 | 3.1 | 2.27 | 1.67 | 28.91 | 15.42 | 17.04 | 264534 | 248163 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8HX | SA488HX | sa48 8hx | sa488hx | Ceredigion | Sir Ceredigion | Cellan WwTW | 676 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 260798 | 249200 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8HY | SA488HY | sa48 8hy | sa488hy | Ceredigion | Sir Ceredigion | Cellan WwTW | 914 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 261015 | 248881 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8HZ | SA488HZ | sa48 8hz | sa488hz | Ceredigion | Sir Ceredigion | Cellan WwTW | 450 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 260549 | 248944 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8JA | SA488JA | sa48 8ja | sa488ja | Ceredigion | Sir Ceredigion | Cellan WwTW | 1258 | 1341 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.99 | 13.33 | 14.73 | 260425 | 247883 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8JB | SA488JB | sa48 8jb | sa488jb | Ceredigion | Sir Ceredigion | Cellan WwTW | 1553 | 1395 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26 | 13.87 | 15.33 | 261448 | 248286 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8JD | SA488JD | sa48 8jd | sa488jd | Ceredigion | Sir Ceredigion | Cellan WwTW | 2484 | 1457 | 1200to1500 | 2.92 | 2.13 | 1.56 | 27.16 | 14.48 | 16.01 | 262578 | 248694 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8JE | SA488JE | sa48 8je | sa488je | Ceredigion | Sir Ceredigion | Cellan WwTW | 1480 | 1406 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.21 | 13.98 | 15.45 | 261605 | 249216 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8JF | SA488JF | sa48 8jf | sa488jf | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 1516 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 262688 | 249815 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8JG | SA488JG | sa48 8jg | sa488jg | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 1554 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 263452 | 250323 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8JH | SA488JH | sa48 8jh | sa488jh | Ceredigion | Sir Ceredigion | Cellan WwTW | 434 | 1349 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.14 | 13.41 | 14.82 | 260247 | 248687 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8JN | SA488JN | sa48 8jn | sa488jn | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 720 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 258349 | 247380 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8JP | SA488JP | sa48 8jp | sa488jp | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 895 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 258517 | 247219 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8JQ | SA488JQ | sa48 8jq | sa488jq | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 2161 | 1488 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.73 | 14.79 | 16.35 | 263957 | 249987 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8JR | SA488JR | sa48 8jr | sa488jr | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1040 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 258653 | 247155 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8JT | SA488JT | sa48 8jt | sa488jt | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1167 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 258748 | 247007 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8JU | SA488JU | sa48 8ju | sa488ju | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 1162 | 1387 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.85 | 13.79 | 15.24 | 258710 | 246912 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8JW | SA488JW | sa48 8jw | sa488jw | Carmarthenshire | Sir Gaerfyrddin | Lampeter STW | 846 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 258476 | 247352 | Carmarthenshire LPA | CA | Afon Teifi/ River Teifi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8JX | SA488JX | sa48 8jx | sa488jx | Ceredigion | Sir Ceredigion | Lampeter STW | 808 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258253 | 247854 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8JY | SA488JY | sa48 8jy | sa488jy | Ceredigion | Sir Ceredigion | Cellan WwTW | 525 | 1349 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.14 | 13.41 | 14.82 | 259616 | 248996 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8JZ | SA488JZ | sa48 8jz | sa488jz | Ceredigion | Sir Ceredigion | Cellan WwTW | 1295 | 1345 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.07 | 13.37 | 14.78 | 261098 | 249964 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LA | SA488LA | sa48 8la | sa488la | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 170 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 262163 | 251416 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LB | SA488LB | sa48 8lb | sa488lb | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 700 | 1317 | 1200to1500 | 2.64 | 1.93 | 1.41 | 24.55 | 13.09 | 14.47 | 262315 | 251943 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LD | SA488LD | sa48 8ld | sa488ld | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 280 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 262464 | 251143 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LE | SA488LE | sa48 8le | sa488le | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 840 | 1356 | 1200to1500 | 2.71 | 1.99 | 1.46 | 25.27 | 13.48 | 14.9 | 262397 | 250434 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LF | SA488LF | sa48 8lf | sa488lf | Ceredigion | Sir Ceredigion | Lampeter STW | 841 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258231 | 247928 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LG | SA488LG | sa48 8lg | sa488lg | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 498 | 1368 | 1200to1500 | 2.74 | 2 | 1.47 | 25.5 | 13.6 | 15.03 | 262704 | 251239 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LH | SA488LH | sa48 8lh | sa488lh | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 1712 | 1393 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.96 | 13.85 | 15.3 | 263576 | 252278 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LJ | SA488LJ | sa48 8lj | sa488lj | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 2191 | 1431 | 1200to1500 | 2.86 | 2.1 | 1.54 | 26.67 | 14.22 | 15.72 | 264381 | 250995 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LL | SA488LL | sa48 8ll | sa488ll | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 2944 | 1490 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.77 | 14.81 | 16.37 | 265187 | 252288 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LQ | SA488LQ | sa48 8lq | sa488lq | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 834 | 1368 | 1200to1500 | 2.74 | 2 | 1.47 | 25.5 | 13.6 | 15.03 | 263023 | 251087 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LS | SA488LS | sa48 8ls | sa488ls | Ceredigion | Sir Ceredigion | Lampeter STW | 1736 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258389 | 248901 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LT | SA488LT | sa48 8lt | sa488lt | Ceredigion | Sir Ceredigion | Lampeter STW | 1631 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 257930 | 248943 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LU | SA488LU | sa48 8lu | sa488lu | Ceredigion | Sir Ceredigion | Cellan WwTW | 2074 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 258316 | 250112 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LX | SA488LX | sa48 8lx | sa488lx | Ceredigion | Sir Ceredigion | Cellan WwTW | 2729 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 258070 | 250896 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LY | SA488LY | sa48 8ly | sa488ly | Ceredigion | Sir Ceredigion | Llangybi STW | 369 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 260385 | 252663 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8LZ | SA488LZ | sa48 8lz | sa488lz | Ceredigion | Sir Ceredigion | Llangybi STW | 213 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 260679 | 252945 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NA | SA488NA | sa48 8na | sa488na | Ceredigion | Sir Ceredigion | Llangybi STW | 228 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 260708 | 253017 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NB | SA488NB | sa48 8nb | sa488nb | Ceredigion | Sir Ceredigion | Llangybi STW | 582 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 261058 | 252956 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8ND | SA488ND | sa48 8nd | sa488nd | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 1487 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 262429 | 252722 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NE | SA488NE | sa48 8ne | sa488ne | Ceredigion | Sir Ceredigion | Llanfair Clydogau WwTW | 781 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 261493 | 251571 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NG | SA488NG | sa48 8ng | sa488ng | Ceredigion | Sir Ceredigion | Llangybi STW | 464 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 260910 | 253193 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NH | SA488NH | sa48 8nh | sa488nh | Ceredigion | Sir Ceredigion | Llangybi STW | 2882 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 262466 | 255108 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NJ | SA488NJ | sa48 8nj | sa488nj | Ceredigion | Sir Ceredigion | Llangybi STW | 2755 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 262248 | 255132 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NL | SA488NL | sa48 8nl | sa488nl | Ceredigion | Sir Ceredigion | Llangybi STW | 2061 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 262285 | 254014 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NN | SA488NN | sa48 8nn | sa488nn | Ceredigion | Sir Ceredigion | Llangybi STW | 1008 | 1296 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.16 | 12.88 | 14.24 | 260130 | 253965 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NP | SA488NP | sa48 8np | sa488np | Ceredigion | Sir Ceredigion | Llangybi STW | 1745 | 1333 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.85 | 13.25 | 14.65 | 259923 | 251367 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NQ | SA488NQ | sa48 8nq | sa488nq | Ceredigion | Sir Ceredigion | Llangybi STW | 1015 | 1292 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.08 | 12.84 | 14.2 | 261195 | 253740 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NR | SA488NR | sa48 8nr | sa488nr | Ceredigion | Sir Ceredigion | Llangybi STW | 297 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 260777 | 253023 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NU | SA488NU | sa48 8nu | sa488nu | Ceredigion | Sir Ceredigion | Cellan WwTW | 2700 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 258448 | 251217 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NX | SA488NX | sa48 8nx | sa488nx | Ceredigion | Sir Ceredigion | Llangybi STW | 1496 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 259397 | 251989 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8NY | SA488NY | sa48 8ny | sa488ny | Ceredigion | Sir Ceredigion | Llangybi STW | 955 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 259818 | 252332 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8PA | SA488PA | sa48 8pa | sa488pa | Ceredigion | Sir Ceredigion | Llangybi STW | 1325 | 1320 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.6 | 13.12 | 14.5 | 259229 | 252584 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8PB | SA488PB | sa48 8pb | sa488pb | Ceredigion | Sir Ceredigion | Llangybi STW | 1866 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 258808 | 253848 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8PD | SA488PD | sa48 8pd | sa488pd | Ceredigion | Sir Ceredigion | Llangybi STW | 1978 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 258848 | 251903 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8PE | SA488PE | sa48 8pe | sa488pe | Ceredigion | Sir Ceredigion | Llangybi STW | 2390 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 258092 | 252932 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 8PF | SA488PF | sa48 8pf | sa488pf | Ceredigion | Sir Ceredigion | Llangybi STW | 3366 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 257330 | 254205 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 9BH | SA489BH | sa48 9bh | sa489bh | Ceredigion | Sir Ceredigion | Lampeter STW | 1152 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258050 | 248412 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SA48 9BT | SA489BT | sa48 9bt | sa489bt | Ceredigion | Sir Ceredigion | Lampeter STW | 1152 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 258050 | 248412 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY23 4HY | SY234HY | sy23 4hy | sy234hy | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 6539 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 266324 | 267730 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY23 4JA | SY234JA | sy23 4ja | sy234ja | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 7494 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 265323 | 267416 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY23 4JB | SY234JB | sy23 4jb | sy234jb | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 8242 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 264549 | 267069 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY23 4JD | SY234JD | sy23 4jd | sy234jd | Ceredigion | Sir Ceredigion | Tregaron WwTW | 9194 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 263433 | 267522 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY23 4JE | SY234JE | sy23 4je | sy234je | Ceredigion | Sir Ceredigion | Tregaron WwTW | 8624 | 1342 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.01 | 13.34 | 14.74 | 263294 | 266821 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY23 4TF | SY234TF | sy23 4tf | sy234tf | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 8688 | 1320 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.6 | 13.12 | 14.5 | 264173 | 267863 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY23 4TG | SY234TG | sy23 4tg | sy234tg | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 8765 | 1349 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.14 | 13.41 | 14.82 | 264047 | 267411 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY23 4TH | SY234TH | sy23 4th | sy234th | Ceredigion | Sir Ceredigion | Tregaron WwTW | 8421 | 1349 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.14 | 13.41 | 14.82 | 264117 | 266975 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY23 4TJ | SY234TJ | sy23 4tj | sy234tj | Ceredigion | Sir Ceredigion | Tregaron WwTW | 7723 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 264243 | 266272 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY23 4TL | SY234TL | sy23 4tl | sy234tl | Ceredigion | Sir Ceredigion | Tregaron WwTW | 5665 | 1317 | 1200to1500 | 2.64 | 1.93 | 1.41 | 24.55 | 13.09 | 14.47 | 264345 | 264021 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY23 4TQ | SY234TQ | sy23 4tq | sy234tq | Ceredigion | Sir Ceredigion | Tregaron WwTW | 8381 | 1349 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.14 | 13.41 | 14.82 | 264115 | 266932 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AA | SY256AA | sy25 6aa | sy256aa | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 2363 | 1356 | 1200to1500 | 2.71 | 1.99 | 1.46 | 25.27 | 13.48 | 14.9 | 270581 | 267567 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AB | SY256AB | sy25 6ab | sy256ab | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 1996 | 1356 | 1200to1500 | 2.71 | 1.99 | 1.46 | 25.27 | 13.48 | 14.9 | 271209 | 267937 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AH | SY256AH | sy25 6ah | sy256ah | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 5069 | 1368 | 1200to1500 | 2.74 | 2 | 1.47 | 25.5 | 13.6 | 15.03 | 267964 | 268281 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AL | SY256AL | sy25 6al | sy256al | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 3533 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 269271 | 266326 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AN | SY256AN | sy25 6an | sy256an | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 3618 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 269257 | 265899 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AP | SY256AP | sy25 6ap | sy256ap | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 5691 | 1326 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.71 | 13.18 | 14.57 | 267122 | 266127 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AR | SY256AR | sy25 6ar | sy256ar | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 374 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 272956 | 266378 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AS | SY256AS | sy25 6as | sy256as | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 459 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 266178 | 255174 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AT | SY256AT | sy25 6at | sy256at | Ceredigion | Sir Ceredigion | Tregaron WwTW | 416 | 1309 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.4 | 13.01 | 14.38 | 267478 | 259520 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AW | SY256AW | sy25 6aw | sy256aw | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 4607 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 268329 | 265533 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AX | SY256AX | sy25 6ax | sy256ax | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 1668 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 271245 | 267357 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AY | SY256AY | sy25 6ay | sy256ay | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 1292 | 1396 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26.02 | 13.88 | 15.34 | 272575 | 267984 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6AZ | SY256AZ | sy25 6az | sy256az | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 343 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 273118 | 266780 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BA | SY256BA | sy25 6ba | sy256ba | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 375 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 273156 | 266691 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BB | SY256BB | sy25 6bb | sy256bb | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 290 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 273059 | 266796 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BD | SY256BD | sy25 6bd | sy256bd | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 298 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 273076 | 266658 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BE | SY256BE | sy25 6be | sy256be | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 380 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 273137 | 266573 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BG | SY256BG | sy25 6bg | sy256bg | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 317 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 273087 | 266624 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BH | SY256BH | sy25 6bh | sy256bh | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 325 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 273077 | 266573 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BJ | SY256BJ | sy25 6bj | sy256bj | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 897 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 273637 | 266437 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BL | SY256BL | sy25 6bl | sy256bl | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 445 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 273158 | 266946 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BN | SY256BN | sy25 6bn | sy256bn | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 3264 | 1506 | Over1500 | 3.01 | 2.21 | 1.62 | 28.07 | 14.97 | 16.55 | 274295 | 269600 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BP | SY256BP | sy25 6bp | sy256bp | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 1802 | 1452 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.06 | 14.43 | 15.95 | 274047 | 267992 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BQ | SY256BQ | sy25 6bq | sy256bq | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 367 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 273124 | 266576 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BS | SY256BS | sy25 6bs | sy256bs | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 2435 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 274962 | 267792 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BT | SY256BT | sy25 6bt | sy256bt | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 3768 | 1631 | Over1500 | 3.26 | 2.39 | 1.75 | 30.4 | 16.21 | 17.92 | 275968 | 268720 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BU | SY256BU | sy25 6bu | sy256bu | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 455 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 273198 | 266893 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6BW | SY256BW | sy25 6bw | sy256bw | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 1794 | 1452 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.06 | 14.43 | 15.95 | 274056 | 267971 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6EB | SY256EB | sy25 6eb | sy256eb | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 399 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 273178 | 266760 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6ED | SY256ED | sy25 6ed | sy256ed | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 315 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 273004 | 266485 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6EE | SY256EE | sy25 6ee | sy256ee | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 333 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 272983 | 266443 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6EF | SY256EF | sy25 6ef | sy256ef | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 385 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 272995 | 266388 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6EG | SY256EG | sy25 6eg | sy256eg | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 432 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 272983 | 266327 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6EH | SY256EH | sy25 6eh | sy256eh | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 291 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 272950 | 266471 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6EJ | SY256EJ | sy25 6ej | sy256ej | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 505 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 272300 | 266558 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6EL | SY256EL | sy25 6el | sy256el | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 1970 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 272275 | 264806 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6EN | SY256EN | sy25 6en | sy256en | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 459 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 273147 | 266431 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6EP | SY256EP | sy25 6ep | sy256ep | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 507 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 273152 | 266362 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6EQ | SY256EQ | sy25 6eq | sy256eq | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 318 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 272922 | 266424 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6ER | SY256ER | sy25 6er | sy256er | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 839 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 273425 | 266171 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6ES | SY256ES | sy25 6es | sy256es | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 3194 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 275494 | 265023 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6ET | SY256ET | sy25 6et | sy256et | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 3484 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 276219 | 266143 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6EU | SY256EU | sy25 6eu | sy256eu | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 380 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 273048 | 266438 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6EW | SY256EW | sy25 6ew | sy256ew | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 451 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 273130 | 266422 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HA | SY256HA | sy25 6ha | sy256ha | Ceredigion | Sir Ceredigion | Tregaron WwTW | 857 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267933 | 259697 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HD | SY256HD | sy25 6hd | sy256hd | Ceredigion | Sir Ceredigion | Tregaron WwTW | 753 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267835 | 259652 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HE | SY256HE | sy25 6he | sy256he | Ceredigion | Sir Ceredigion | Tregaron WwTW | 749 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267865 | 259608 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HF | SY256HF | sy25 6hf | sy256hf | Ceredigion | Sir Ceredigion | Tregaron WwTW | 744 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267846 | 259624 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HG | SY256HG | sy25 6hg | sy256hg | Ceredigion | Sir Ceredigion | Tregaron WwTW | 426 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 267568 | 259460 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HH | SY256HH | sy25 6hh | sy256hh | Ceredigion | Sir Ceredigion | Tregaron WwTW | 958 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268000 | 259775 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HJ | SY256HJ | sy25 6hj | sy256hj | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1034 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268012 | 259875 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HL | SY256HL | sy25 6hl | sy256hl | Ceredigion | Sir Ceredigion | Tregaron WwTW | 2422 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 269489 | 260113 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HN | SY256HN | sy25 6hn | sy256hn | Ceredigion | Sir Ceredigion | Tregaron WwTW | 4228 | 1446 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.95 | 14.37 | 15.89 | 271093 | 260949 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HP | SY256HP | sy25 6hp | sy256hp | Ceredigion | Sir Ceredigion | Tregaron WwTW | 492 | 1309 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.4 | 13.01 | 14.38 | 267490 | 259600 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HQ | SY256HQ | sy25 6hq | sy256hq | Ceredigion | Sir Ceredigion | Tregaron WwTW | 805 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267846 | 259718 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HR | SY256HR | sy25 6hr | sy256hr | Ceredigion | Sir Ceredigion | Tregaron WwTW | 651 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267644 | 259691 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HU | SY256HU | sy25 6hu | sy256hu | Ceredigion | Sir Ceredigion | Tregaron WwTW | 884 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267925 | 259748 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HW | SY256HW | sy25 6hw | sy256hw | Ceredigion | Sir Ceredigion | Tregaron WwTW | 517 | 1309 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.4 | 13.01 | 14.38 | 267239 | 259681 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HX | SY256HX | sy25 6hx | sy256hx | Ceredigion | Sir Ceredigion | Tregaron WwTW | 980 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267913 | 259896 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HY | SY256HY | sy25 6hy | sy256hy | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1176 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267916 | 260141 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6HZ | SY256HZ | sy25 6hz | sy256hz | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1120 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267885 | 260095 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JA | SY256JA | sy25 6ja | sy256ja | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1174 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268057 | 260027 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JB | SY256JB | sy25 6jb | sy256jb | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1155 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267957 | 260087 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JD | SY256JD | sy25 6jd | sy256jd | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1216 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268117 | 260028 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JE | SY256JE | sy25 6je | sy256je | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1263 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268075 | 260131 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JF | SY256JF | sy25 6jf | sy256jf | Ceredigion | Sir Ceredigion | Tregaron WwTW | 3178 | 1347 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.11 | 13.39 | 14.8 | 268815 | 261936 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JG | SY256JG | sy25 6jg | sy256jg | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1381 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268245 | 260134 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JH | SY256JH | sy25 6jh | sy256jh | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1364 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268157 | 260193 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JL | SY256JL | sy25 6jl | sy256jl | Ceredigion | Sir Ceredigion | Tregaron WwTW | 952 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268036 | 259717 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JN | SY256JN | sy25 6jn | sy256jn | Ceredigion | Sir Ceredigion | Tregaron WwTW | 879 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267997 | 259646 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JP | SY256JP | sy25 6jp | sy256jp | Ceredigion | Sir Ceredigion | Tregaron WwTW | 520 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 267775 | 259245 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JQ | SY256JQ | sy25 6jq | sy256jq | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1255 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268006 | 260175 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JR | SY256JR | sy25 6jr | sy256jr | Ceredigion | Sir Ceredigion | Tregaron WwTW | 706 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 267602 | 258547 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JS | SY256JS | sy25 6js | sy256js | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1835 | 1483 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.64 | 14.74 | 16.29 | 268779 | 258135 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JT | SY256JT | sy25 6jt | sy256jt | Ceredigion | Sir Ceredigion | Tregaron WwTW | 807 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267915 | 259637 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JU | SY256JU | sy25 6ju | sy256ju | Ceredigion | Sir Ceredigion | Tregaron WwTW | 758 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267895 | 259581 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JW | SY256JW | sy25 6jw | sy256jw | Ceredigion | Sir Ceredigion | Tregaron WwTW | 639 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 267884 | 259306 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JX | SY256JX | sy25 6jx | sy256jx | Ceredigion | Sir Ceredigion | Tregaron WwTW | 998 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268121 | 259671 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JY | SY256JY | sy25 6jy | sy256jy | Ceredigion | Sir Ceredigion | Tregaron WwTW | 682 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 267828 | 259543 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6JZ | SY256JZ | sy25 6jz | sy256jz | Ceredigion | Sir Ceredigion | Tregaron WwTW | 685 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 267865 | 259488 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6LA | SY256LA | sy25 6la | sy256la | Ceredigion | Sir Ceredigion | Tregaron WwTW | 638 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 267828 | 259457 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6LG | SY256LG | sy25 6lg | sy256lg | Ceredigion | Sir Ceredigion | Tregaron WwTW | 2280 | 1296 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.16 | 12.88 | 14.24 | 266912 | 261418 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6LH | SY256LH | sy25 6lh | sy256lh | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1657 | 1301 | 1200to1500 | 2.6 | 1.91 | 1.4 | 24.25 | 12.93 | 14.29 | 266343 | 260544 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6LJ | SY256LJ | sy25 6lj | sy256lj | Ceredigion | Sir Ceredigion | Tregaron WwTW | 2741 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 265908 | 261548 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6LL | SY256LL | sy25 6ll | sy256ll | Ceredigion | Sir Ceredigion | Tregaron WwTW | 3306 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 266203 | 262296 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6LN | SY256LN | sy25 6ln | sy256ln | Ceredigion | Sir Ceredigion | Tregaron WwTW | 4410 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 265249 | 263088 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6LQ | SY256LQ | sy25 6lq | sy256lq | Ceredigion | Sir Ceredigion | Tregaron WwTW | 3098 | 1305 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.32 | 12.97 | 14.34 | 266710 | 262213 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6LR | SY256LR | sy25 6lr | sy256lr | Ceredigion | Sir Ceredigion | Tregaron WwTW | 5354 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 265241 | 264122 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6LS | SY256LS | sy25 6ls | sy256ls | Ceredigion | Sir Ceredigion | Tregaron WwTW | 6853 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 265235 | 265710 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6LT | SY256LT | sy25 6lt | sy256lt | Ceredigion | Sir Ceredigion | Tregaron WwTW | 5880 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 264758 | 264484 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6LW | SY256LW | sy25 6lw | sy256lw | Ceredigion | Sir Ceredigion | Tregaron WwTW | 5011 | 1311 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.43 | 13.03 | 14.4 | 266365 | 264094 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6NB | SY256NB | sy25 6nb | sy256nb | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1025 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268131 | 259707 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6ND | SY256ND | sy25 6nd | sy256nd | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1111 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268202 | 259756 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6NE | SY256NE | sy25 6ne | sy256ne | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1073 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268172 | 259732 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6NF | SY256NF | sy25 6nf | sy256nf | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1092 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268218 | 259690 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6NG | SY256NG | sy25 6ng | sy256ng | Ceredigion | Sir Ceredigion | Tregaron WwTW | 2000 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 269205 | 259632 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6NH | SY256NH | sy25 6nh | sy256nh | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1458 | 1446 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.95 | 14.37 | 15.89 | 268716 | 259252 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6NJ | SY256NJ | sy25 6nj | sy256nj | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1589 | 1446 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.95 | 14.37 | 15.89 | 268825 | 259443 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6NL | SY256NL | sy25 6nl | sy256nl | Ceredigion | Sir Ceredigion | Tregaron WwTW | 2238 | 1446 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.95 | 14.37 | 15.89 | 269403 | 258518 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6NN | SY256NN | sy25 6nn | sy256nn | Ceredigion | Sir Ceredigion | Tregaron WwTW | 3579 | 1654 | Over1500 | 3.31 | 2.42 | 1.78 | 30.83 | 16.44 | 18.17 | 270717 | 258239 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6NY | SY256NY | sy25 6ny | sy256ny | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 1063 | 1395 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26 | 13.87 | 15.33 | 265145 | 254289 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6NZ | SY256NZ | sy25 6nz | sy256nz | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 1350 | 1362 | 1200to1500 | 2.73 | 1.99 | 1.46 | 25.39 | 13.54 | 14.96 | 264540 | 254525 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PA | SY256PA | sy25 6pa | sy256pa | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 2098 | 1333 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.85 | 13.25 | 14.65 | 263809 | 254316 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PB | SY256PB | sy25 6pb | sy256pb | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 2474 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 263261 | 255463 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PD | SY256PD | sy25 6pd | sy256pd | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 906 | 1445 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.93 | 14.36 | 15.88 | 266527 | 255592 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PE | SY256PE | sy25 6pe | sy256pe | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 968 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 266028 | 254266 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PF | SY256PF | sy25 6pf | sy256pf | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 3399 | 1602 | Over1500 | 3.21 | 2.35 | 1.72 | 29.86 | 15.92 | 17.6 | 269082 | 254694 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PP | SY256PP | sy25 6pp | sy256pp | Ceredigion | Sir Ceredigion | Tregaron WwTW | 829 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 266794 | 258480 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PR | SY256PR | sy25 6pr | sy256pr | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1951 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 265846 | 257823 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PS | SY256PS | sy25 6ps | sy256ps | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 1947 | 1315 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.51 | 13.07 | 14.45 | 265259 | 257075 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PT | SY256PT | sy25 6pt | sy256pt | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 2393 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 264397 | 257177 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PU | SY256PU | sy25 6pu | sy256pu | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 2879 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 264174 | 257612 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PX | SY256PX | sy25 6px | sy256px | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 3919 | 1267 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.61 | 12.59 | 13.92 | 262804 | 257801 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6QS | SY256QS | sy25 6qs | sy256qs | Ceredigion | Sir Ceredigion | Tregaron WwTW | 188 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 267447 | 259141 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6QT | SY256QT | sy25 6qt | sy256qt | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1179 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 266087 | 259058 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6QU | SY256QU | sy25 6qu | sy256qu | Ceredigion | Sir Ceredigion | Tregaron WwTW | 3576 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 263688 | 259039 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6RL | SY256RL | sy25 6rl | sy256rl | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 592 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 266289 | 255343 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6RN | SY256RN | sy25 6rn | sy256rn | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 597 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 266309 | 255276 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6RP | SY256RP | sy25 6rp | sy256rp | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 468 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 266148 | 255369 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6RR | SY256RR | sy25 6rr | sy256rr | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 372 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 266084 | 255253 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6RS | SY256RS | sy25 6rs | sy256rs | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 435 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 266151 | 255233 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6RT | SY256RT | sy25 6rt | sy256rt | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 237 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 265956 | 255182 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6RU | SY256RU | sy25 6ru | sy256ru | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 507 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 266222 | 255245 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6RW | SY256RW | sy25 6rw | sy256rw | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 588 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 266238 | 255459 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6RX | SY256RX | sy25 6rx | sy256rx | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 654 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 266372 | 255206 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6RY | SY256RY | sy25 6ry | sy256ry | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 625 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 266343 | 255217 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6RZ | SY256RZ | sy25 6rz | sy256rz | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 638 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 266355 | 255131 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6SA | SY256SA | sy25 6sa | sy256sa | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 691 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 266410 | 255178 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6SB | SY256SB | sy25 6sb | sy256sb | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 986 | 1503 | Over1500 | 3.01 | 2.2 | 1.61 | 28.01 | 14.94 | 16.51 | 266651 | 254863 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6SZ | SY256SZ | sy25 6sz | sy256sz | Ceredigion | Sir Ceredigion | Tregaron WwTW | 3198 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 264079 | 259478 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6TB | SY256TB | sy25 6tb | sy256tb | Ceredigion | Sir Ceredigion | Tregaron WwTW | 2916 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 264347 | 259075 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6TD | SY256TD | sy25 6td | sy256td | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 3878 | 1267 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.61 | 12.59 | 13.92 | 263238 | 258163 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6TE | SY256TE | sy25 6te | sy256te | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 4791 | 1254 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.37 | 12.47 | 13.78 | 261986 | 258185 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6UG | SY256UG | sy25 6ug | sy256ug | Ceredigion | Sir Ceredigion | Tregaron WwTW | 1521 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 267174 | 257647 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6UH | SY256UH | sy25 6uh | sy256uh | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 443 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 265868 | 255600 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6UJ | SY256UJ | sy25 6uj | sy256uj | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 724 | 1339 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.96 | 13.31 | 14.71 | 265466 | 255861 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6UL | SY256UL | sy25 6ul | sy256ul | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 1753 | 1315 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.51 | 13.07 | 14.45 | 265211 | 256860 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6UN | SY256UN | sy25 6un | sy256un | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 2162 | 1315 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.51 | 13.07 | 14.45 | 264562 | 257009 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6UP | SY256UP | sy25 6up | sy256up | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 3106 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 262797 | 256236 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6UQ | SY256UQ | sy25 6uq | sy256uq | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 1207 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 266277 | 256253 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6UR | SY256UR | sy25 6ur | sy256ur | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 2863 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 263003 | 256086 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6UT | SY256UT | sy25 6ut | sy256ut | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 552 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 266069 | 255610 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6UU | SY256UU | sy25 6uu | sy256uu | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 676 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 266143 | 255709 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6UW | SY256UW | sy25 6uw | sy256uw | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 2028 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 264219 | 256548 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6WN | SY256WN | sy25 6wn | sy256wn | Ceredigion | Sir Ceredigion | Tregaron WwTW | 945 | 1335 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.88 | 13.27 | 14.67 | 268026 | 259719 | Ceredigion LPA | CE | Afon Teifi/ River Teifi | Cyngor Sir Ceredigion | Ceredigion County Council
LD3 8RE | LD38RE | ld3 8re | ld38re | Powys | Powys | Trecastle WwTW | 2673 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 287160 | 231389 | Powys LPA | PO | Afon Tywi/ River Tywi | Cyngor Sir Powys | Powys County Council
LD3 8RF | LD38RF | ld3 8rf | ld38rf | Powys | Powys | Trecastle WwTW | 1959 | 1687 | Over1500 | 3.38 | 2.47 | 1.81 | 31.44 | 16.77 | 18.53 | 286321 | 229829 | Brecon Beacons National Park LPA | PO | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
LD3 8RG | LD38RG | ld3 8rg | ld38rg | Powys | Powys | Trecastle WwTW | 2460 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 286900 | 231047 | Powys LPA | PO | Afon Tywi/ River Tywi | Cyngor Sir Powys | Powys County Council
LD3 8RH | LD38RH | ld3 8rh | ld38rh | Powys | Powys | Trecastle WwTW | 4016 | 1536 | Over1500 | 3.07 | 2.25 | 1.65 | 28.63 | 15.27 | 16.88 | 285102 | 231615 | Powys LPA | PO | Afon Tywi/ River Tywi | Cyngor Sir Powys | Powys County Council
SA14 7TB | SA147TB | sa14 7tb | sa147tb | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 4648 | 1626 | Over1500 | 3.25 | 2.38 | 1.75 | 30.31 | 16.16 | 17.86 | 255697 | 218035 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LX | SA182LX | sa18 2lx | sa182lx | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 3031 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 262471 | 217986 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2LZ | SA182LZ | sa18 2lz | sa182lz | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 2616 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 262822 | 218267 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NJ | SA182NJ | sa18 2nj | sa182nj | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 3282 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 262107 | 217930 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NQ | SA182NQ | sa18 2nq | sa182nq | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 3232 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 262283 | 217914 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NX | SA182NX | sa18 2nx | sa182nx | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 3306 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 262010 | 217891 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2NZ | SA182NZ | sa18 2nz | sa182nz | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 3085 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 261896 | 218101 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2TS | SA182TS | sa18 2ts | sa182ts | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 1995 | 1539 | Over1500 | 3.08 | 2.25 | 1.65 | 28.68 | 15.3 | 16.91 | 263851 | 217596 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 2TT | SA182TT | sa18 2tt | sa182tt | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 2116 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 263452 | 217986 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA18 3LJ | SA183LJ | sa18 3lj | sa183lj | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2608 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 260829 | 218676 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 0AD | SA190AD | sa19 0ad | sa190ad | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2705 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263260 | 223298 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 0AE | SA190AE | sa19 0ae | sa190ae | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2705 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263260 | 223298 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 0AQ | SA190AQ | sa19 0aq | sa190aq | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2705 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263260 | 223298 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 0AR | SA190AR | sa19 0ar | sa190ar | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2705 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263260 | 223298 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 0AU | SA190AU | sa19 0au | sa190au | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2705 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263260 | 223298 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 0AW | SA190AW | sa19 0aw | sa190aw | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2705 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263260 | 223298 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 0BA | SA190BA | sa19 0ba | sa190ba | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2705 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263260 | 223298 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 0BB | SA190BB | sa19 0bb | sa190bb | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2705 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263260 | 223298 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AA | SA196AA | sa19 6aa | sa196aa | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1728 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262884 | 222315 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AE | SA196AE | sa19 6ae | sa196ae | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1746 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262862 | 222365 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AH | SA196AH | sa19 6ah | sa196ah | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1729 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262870 | 222332 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AJ | SA196AJ | sa19 6aj | sa196aj | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2142 | 1472 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.44 | 14.63 | 16.17 | 262275 | 223199 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AN | SA196AN | sa19 6an | sa196an | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1709 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262793 | 222383 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AP | SA196AP | sa19 6ap | sa196ap | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1765 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262830 | 222426 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AQ | SA196AQ | sa19 6aq | sa196aq | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 497 | 1458 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.17 | 14.49 | 16.02 | 268674 | 225285 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6AR | SA196AR | sa19 6ar | sa196ar | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1765 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262849 | 222406 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AS | SA196AS | sa19 6as | sa196as | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1674 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262780 | 222347 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AT | SA196AT | sa19 6at | sa196at | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1625 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262781 | 222275 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AU | SA196AU | sa19 6au | sa196au | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1633 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262798 | 222269 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AW | SA196AW | sa19 6aw | sa196aw | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1697 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262743 | 222415 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AX | SA196AX | sa19 6ax | sa196ax | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2516 | 1452 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.06 | 14.43 | 15.95 | 262328 | 223575 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AY | SA196AY | sa19 6ay | sa196ay | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1623 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262826 | 222221 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6AZ | SA196AZ | sa19 6az | sa196az | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2405 | 1452 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.06 | 14.43 | 15.95 | 261944 | 223548 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6BA | SA196BA | sa19 6ba | sa196ba | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1701 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262850 | 222313 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6BD | SA196BD | sa19 6bd | sa196bd | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1803 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262976 | 222322 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6BG | SA196BG | sa19 6bg | sa196bg | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1854 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 263063 | 222296 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6BH | SA196BH | sa19 6bh | sa196bh | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1710 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262944 | 222214 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6BJ | SA196BJ | sa19 6bj | sa196bj | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1730 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262756 | 222448 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6BL | SA196BL | sa19 6bl | sa196bl | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1657 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262918 | 222161 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6BN | SA196BN | sa19 6bn | sa196bn | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1536 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262805 | 222109 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6BQ | SA196BQ | sa19 6bq | sa196bq | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1608 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262834 | 222189 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6BS | SA196BS | sa19 6bs | sa196bs | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1868 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262945 | 222455 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6BU | SA196BU | sa19 6bu | sa196bu | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1873 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262926 | 222482 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DA | SA196DA | sa19 6da | sa196da | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1817 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262890 | 222439 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DB | SA196DB | sa19 6db | sa196db | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1951 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262978 | 222541 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DD | SA196DD | sa19 6dd | sa196dd | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1862 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262879 | 222513 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DF | SA196DF | sa19 6df | sa196df | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1779 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262774 | 222497 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DH | SA196DH | sa19 6dh | sa196dh | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1818 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262812 | 222515 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DL | SA196DL | sa19 6dl | sa196dl | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1678 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262690 | 222437 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DN | SA196DN | sa19 6dn | sa196dn | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1871 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262830 | 222571 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DP | SA196DP | sa19 6dp | sa196dp | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1843 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262776 | 222580 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DR | SA196DR | sa19 6dr | sa196dr | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1828 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262756 | 222577 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DS | SA196DS | sa19 6ds | sa196ds | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1875 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262803 | 222599 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DT | SA196DT | sa19 6dt | sa196dt | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1890 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262815 | 222609 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DU | SA196DU | sa19 6du | sa196du | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1928 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262775 | 222690 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DW | SA196DW | sa19 6dw | sa196dw | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1915 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262870 | 222594 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DX | SA196DX | sa19 6dx | sa196dx | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1808 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262770 | 222539 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DY | SA196DY | sa19 6dy | sa196dy | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1973 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262757 | 222761 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6DZ | SA196DZ | sa19 6dz | sa196dz | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1875 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262873 | 222537 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6EA | SA196EA | sa19 6ea | sa196ea | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1983 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262801 | 222740 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6EB | SA196EB | sa19 6eb | sa196eb | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2025 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262935 | 222683 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6ED | SA196ED | sa19 6ed | sa196ed | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2118 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262933 | 222807 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6EE | SA196EE | sa19 6ee | sa196ee | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2065 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262931 | 222740 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6EF | SA196EF | sa19 6ef | sa196ef | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2133 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263032 | 222741 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6EG | SA196EG | sa19 6eg | sa196eg | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2015 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262741 | 222823 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6EN | SA196EN | sa19 6en | sa196en | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1821 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262957 | 222373 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6EP | SA196EP | sa19 6ep | sa196ep | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1858 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262957 | 222428 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6HA | SA196HA | sa19 6ha | sa196ha | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1904 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262995 | 222455 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6HD | SA196HD | sa19 6hd | sa196hd | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1963 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263029 | 222505 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6HF | SA196HF | sa19 6hf | sa196hf | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1929 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262993 | 222493 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6HJ | SA196HJ | sa19 6hj | sa196hj | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1901 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 263003 | 222441 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6HL | SA196HL | sa19 6hl | sa196hl | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2024 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263099 | 222518 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6HN | SA196HN | sa19 6hn | sa196hn | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1962 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 263106 | 222415 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6HS | SA196HS | sa19 6hs | sa196hs | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2085 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263175 | 222524 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6HT | SA196HT | sa19 6ht | sa196ht | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2090 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263128 | 222584 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6HU | SA196HU | sa19 6hu | sa196hu | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2180 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263213 | 222625 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6HW | SA196HW | sa19 6hw | sa196hw | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1917 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 263089 | 222365 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6HY | SA196HY | sa19 6hy | sa196hy | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2148 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263241 | 222543 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6LA | SA196LA | sa19 6la | sa196la | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2174 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263269 | 222551 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6LB | SA196LB | sa19 6lb | sa196lb | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2262 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263255 | 222701 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6LD | SA196LD | sa19 6ld | sa196ld | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2255 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263291 | 222650 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6LE | SA196LE | sa19 6le | sa196le | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2243 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263299 | 222622 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6LF | SA196LF | sa19 6lf | sa196lf | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2304 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263318 | 222693 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6LU | SA196LU | sa19 6lu | sa196lu | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2329 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263183 | 222868 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6LW | SA196LW | sa19 6lw | sa196lw | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2100 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263102 | 222627 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6ND | SA196ND | sa19 6nd | sa196nd | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2231 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263217 | 222696 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6NE | SA196NE | sa19 6ne | sa196ne | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2319 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263258 | 222781 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6NF | SA196NF | sa19 6nf | sa196nf | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2349 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263309 | 222770 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6NG | SA196NG | sa19 6ng | sa196ng | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2431 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263302 | 222896 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6NL | SA196NL | sa19 6nl | sa196nl | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2431 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263302 | 222896 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6NN | SA196NN | sa19 6nn | sa196nn | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2352 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263242 | 222843 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6NP | SA196NP | sa19 6np | sa196np | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 2860 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 263696 | 223595 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6NR | SA196NR | sa19 6nr | sa196nr | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 2516 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 263921 | 223918 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6NS | SA196NS | sa19 6ns | sa196ns | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 2423 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 264020 | 223926 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6NT | SA196NT | sa19 6nt | sa196nt | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 2398 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 264037 | 223947 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6NU | SA196NU | sa19 6nu | sa196nu | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 2325 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 264097 | 223993 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6NW | SA196NW | sa19 6nw | sa196nw | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2695 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263295 | 223257 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6NX | SA196NX | sa19 6nx | sa196nx | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2374 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263198 | 222916 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PA | SA196PA | sa19 6pa | sa196pa | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1080 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 262626 | 221473 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PB | SA196PB | sa19 6pb | sa196pb | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 894 | 1465 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.31 | 14.56 | 16.1 | 259801 | 221531 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PD | SA196PD | sa19 6pd | sa196pd | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1177 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 262740 | 221418 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PE | SA196PE | sa19 6pe | sa196pe | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 532 | 1458 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.17 | 14.49 | 16.02 | 262047 | 221443 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PF | SA196PF | sa19 6pf | sa196pf | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 498 | 1455 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.12 | 14.46 | 15.99 | 261122 | 221000 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PG | SA196PG | sa19 6pg | sa196pg | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1147 | 1454 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.1 | 14.45 | 15.97 | 260443 | 221181 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PH | SA196PH | sa19 6ph | sa196ph | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1975 | 1494 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.85 | 14.85 | 16.41 | 263361 | 220296 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PL | SA196PL | sa19 6pl | sa196pl | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1549 | 1494 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.85 | 14.85 | 16.41 | 262913 | 220364 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PN | SA196PN | sa19 6pn | sa196pn | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1713 | 1494 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.85 | 14.85 | 16.41 | 262972 | 220159 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PP | SA196PP | sa19 6pp | sa196pp | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1452 | 1494 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.85 | 14.85 | 16.41 | 262688 | 220220 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PR | SA196PR | sa19 6pr | sa196pr | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1761 | 1502 | Over1500 | 3.01 | 2.2 | 1.61 | 27.99 | 14.93 | 16.5 | 262231 | 219530 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PS | SA196PS | sa19 6ps | sa196ps | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2186 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 261266 | 219009 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PT | SA196PT | sa19 6pt | sa196pt | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2317 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 261668 | 218855 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PU | SA196PU | sa19 6pu | sa196pu | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 2744 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 262660 | 218411 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6PY | SA196PY | sa19 6py | sa196py | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 2171 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 263190 | 218964 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RA | SA196RA | sa19 6ra | sa196ra | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 1638 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 263919 | 219679 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RB | SA196RB | sa19 6rb | sa196rb | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 1654 | 1521 | Over1500 | 3.04 | 2.23 | 1.63 | 28.35 | 15.12 | 16.71 | 263769 | 219350 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RD | SA196RD | sa19 6rd | sa196rd | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 1274 | 1521 | Over1500 | 3.04 | 2.23 | 1.63 | 28.35 | 15.12 | 16.71 | 264090 | 218997 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RE | SA196RE | sa19 6re | sa196re | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 1315 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 265035 | 220174 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6RF | SA196RF | sa19 6rf | sa196rf | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 1152 | 1597 | Over1500 | 3.2 | 2.34 | 1.72 | 29.77 | 15.87 | 17.55 | 266525 | 221192 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6RG | SA196RG | sa19 6rg | sa196rg | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 784 | 1597 | Over1500 | 3.2 | 2.34 | 1.72 | 29.77 | 15.87 | 17.55 | 266763 | 221477 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6RH | SA196RH | sa19 6rh | sa196rh | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 1334 | 1500 |  | 3 | 2.2 | 1.61 | 27.96 | 14.91 | 16.48 | 266018 | 222040 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6RJ | SA196RJ | sa19 6rj | sa196rj | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1858 | 1472 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.44 | 14.63 | 16.17 | 262493 | 222794 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RP | SA196RP | sa19 6rp | sa196rp | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1671 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262596 | 222504 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RR | SA196RR | sa19 6rr | sa196rr | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1836 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262647 | 222671 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RS | SA196RS | sa19 6rs | sa196rs | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1914 | 1472 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.44 | 14.63 | 16.17 | 262423 | 222893 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RT | SA196RT | sa19 6rt | sa196rt | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1374 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 261430 | 222534 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RU | SA196RU | sa19 6ru | sa196ru | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1987 | 1472 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.44 | 14.63 | 16.17 | 261851 | 223139 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RW | SA196RW | sa19 6rw | sa196rw | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1955 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262513 | 222893 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RX | SA196RX | sa19 6rx | sa196rx | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1871 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262574 | 222761 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RY | SA196RY | sa19 6ry | sa196ry | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2616 | 1468 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.36 | 14.59 | 16.13 | 260651 | 223611 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6RZ | SA196RZ | sa19 6rz | sa196rz | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2026 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 262620 | 222914 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SA | SA196SA | sa19 6sa | sa196sa | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 2614 | 1459 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.19 | 14.5 | 16.03 | 260411 | 223530 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SD | SA196SD | sa19 6sd | sa196sd | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 2445 | 1459 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.19 | 14.5 | 16.03 | 259828 | 223653 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SE | SA196SE | sa19 6se | sa196se | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 1387 | 1451 | 1200to1500 | 2.9 | 2.13 | 1.56 | 27.04 | 14.42 | 15.94 | 258544 | 223363 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SF | SA196SF | sa19 6sf | sa196sf | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 1384 | 1451 | 1200to1500 | 2.9 | 2.13 | 1.56 | 27.04 | 14.42 | 15.94 | 258866 | 222921 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SG | SA196SG | sa19 6sg | sa196sg | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 1842 | 1478 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.55 | 14.69 | 16.24 | 259629 | 223083 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SH | SA196SH | sa19 6sh | sa196sh | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 2066 | 1478 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.55 | 14.69 | 16.24 | 260257 | 222958 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SL | SA196SL | sa19 6sl | sa196sl | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 1137 | 1465 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.31 | 14.56 | 16.1 | 259587 | 222304 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SN | SA196SN | sa19 6sn | sa196sn | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 2086 | 1478 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.55 | 14.69 | 16.24 | 259874 | 223238 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SR | SA196SR | sa19 6sr | sa196sr | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1427 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262946 | 221614 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SS | SA196SS | sa19 6ss | sa196ss | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1345 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262719 | 221901 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6ST | SA196ST | sa19 6st | sa196st | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1321 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262828 | 221631 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SU | SA196SU | sa19 6su | sa196su | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1362 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 262896 | 221555 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SY | SA196SY | sa19 6sy | sa196sy | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1491 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 263042 | 221506 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6SZ | SA196SZ | sa19 6sz | sa196sz | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1397 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 262958 | 221452 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6TD | SA196TD | sa19 6td | sa196td | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1979 | 1478 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.55 | 14.69 | 16.24 | 263568 | 221236 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6TE | SA196TE | sa19 6te | sa196te | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 2437 | 1491 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.79 | 14.82 | 16.38 | 264930 | 221717 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6TF | SA196TF | sa19 6tf | sa196tf | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 2179 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 265007 | 221050 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6TG | SA196TG | sa19 6tg | sa196tg | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 2070 | 1478 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.55 | 14.69 | 16.24 | 264083 | 220529 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6TH | SA196TH | sa19 6th | sa196th | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 1213 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 264726 | 219934 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6TL | SA196TL | sa19 6tl | sa196tl | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 316 | 1558 | Over1500 | 3.12 | 2.28 | 1.67 | 29.04 | 15.49 | 17.12 | 265066 | 219017 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6TN | SA196TN | sa19 6tn | sa196tn | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 147 | 1558 | Over1500 | 3.12 | 2.28 | 1.67 | 29.04 | 15.49 | 17.12 | 265357 | 219047 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6TP | SA196TP | sa19 6tp | sa196tp | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 31 | 1558 | Over1500 | 3.12 | 2.28 | 1.67 | 29.04 | 15.49 | 17.12 | 265382 | 218878 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6TR | SA196TR | sa19 6tr | sa196tr | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 430 | 1558 | Over1500 | 3.12 | 2.28 | 1.67 | 29.04 | 15.49 | 17.12 | 264987 | 218686 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6TS | SA196TS | sa19 6ts | sa196ts | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 1349 | 1574 | Over1500 | 3.15 | 2.31 | 1.69 | 29.34 | 15.65 | 17.29 | 264526 | 217840 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6TT | SA196TT | sa19 6tt | sa196tt | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 1156 | 1620 | Over1500 | 3.24 | 2.37 | 1.74 | 30.19 | 16.1 | 17.8 | 266040 | 217965 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6TW | SA196TW | sa19 6tw | sa196tw | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 152 | 1558 | Over1500 | 3.12 | 2.28 | 1.67 | 29.04 | 15.49 | 17.12 | 265314 | 219045 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6TY | SA196TY | sa19 6ty | sa196ty | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 686 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 265917 | 219300 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6UA | SA196UA | sa19 6ua | sa196ua | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 1427 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 266732 | 219291 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6UB | SA196UB | sa19 6ub | sa196ub | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 1309 | 1560 | Over1500 | 3.12 | 2.28 | 1.68 | 29.08 | 15.51 | 17.14 | 266472 | 219590 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6UD | SA196UD | sa19 6ud | sa196ud | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 2353 | 1686 | Over1500 | 3.37 | 2.47 | 1.81 | 31.42 | 16.76 | 18.52 | 267974 | 219726 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6UH | SA196UH | sa19 6uh | sa196uh | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1280 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 262866 | 221268 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6UL | SA196UL | sa19 6ul | sa196ul | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1321 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 262910 | 221128 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6UN | SA196UN | sa19 6un | sa196un | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1355 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 262935 | 221008 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6UR | SA196UR | sa19 6ur | sa196ur | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1711 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 263236 | 221637 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6US | SA196US | sa19 6us | sa196us | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2119 | 1445 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.93 | 14.36 | 15.88 | 263570 | 221923 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6UT | SA196UT | sa19 6ut | sa196ut | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2818 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 264004 | 222622 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6UU | SA196UU | sa19 6uu | sa196uu | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2774 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 263991 | 222558 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6UW | SA196UW | sa19 6uw | sa196uw | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1442 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 262926 | 220627 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6UY | SA196UY | sa19 6uy | sa196uy | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2946 | 1445 | 1200to1500 | 2.89 | 2.12 | 1.55 | 26.93 | 14.36 | 15.88 | 264245 | 222445 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6YA | SA196YA | sa19 6ya | sa196ya | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 1847 | 1481 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.6 | 14.72 | 16.27 | 265331 | 223317 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6YB | SA196YB | sa19 6yb | sa196yb | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 1197 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 265847 | 223799 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6YD | SA196YD | sa19 6yd | sa196yd | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 1024 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 267078 | 224374 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6YE | SA196YE | sa19 6ye | sa196ye | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 929 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 267291 | 224942 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6YF | SA196YF | sa19 6yf | sa196yf | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 847 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 267584 | 224594 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6YG | SA196YG | sa19 6yg | sa196yg | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 94 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 268189 | 225096 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6YH | SA196YH | sa19 6yh | sa196yh | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 301 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 268483 | 225236 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6YL | SA196YL | sa19 6yl | sa196yl | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 580 | 1458 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.17 | 14.49 | 16.02 | 268735 | 225376 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6YN | SA196YN | sa19 6yn | sa196yn | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 698 | 1458 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.17 | 14.49 | 16.02 | 268880 | 225265 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 6YP | SA196YP | sa19 6yp | sa196yp | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 1525 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 267705 | 223743 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6YS | SA196YS | sa19 6ys | sa196ys | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 187 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 267508 | 222096 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6YT | SA196YT | sa19 6yt | sa196yt | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 1120 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 266882 | 223012 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6YU | SA196YU | sa19 6yu | sa196yu | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 2214 | 1481 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.6 | 14.72 | 16.27 | 265207 | 222546 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6YW | SA196YW | sa19 6yw | sa196yw | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 538 | 1458 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.17 | 14.49 | 16.02 | 268579 | 224822 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 6YY | SA196YY | sa19 6yy | sa196yy | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 1665 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 268232 | 223526 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 7AA | SA197AA | sa19 7aa | sa197aa | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 2888 | 1459 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.19 | 14.5 | 16.03 | 259688 | 224343 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AB | SA197AB | sa19 7ab | sa197ab | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 2599 | 1469 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.38 | 14.6 | 16.14 | 259194 | 224397 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AD | SA197AD | sa19 7ad | sa197ad | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 2993 | 1497 | 1200to1500 | 3 | 2.19 | 1.61 | 27.9 | 14.88 | 16.45 | 259203 | 224870 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AE | SA197AE | sa19 7ae | sa197ae | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 1918 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 258497 | 224037 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AF | SA197AF | sa19 7af | sa197af | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 2306 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 264091 | 224056 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AG | SA197AG | sa19 7ag | sa197ag | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 1396 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 264851 | 224674 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AH | SA197AH | sa19 7ah | sa197ah | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 656 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 265566 | 224954 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AJ | SA197AJ | sa19 7aj | sa197aj | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 850 | 1579 | Over1500 | 3.16 | 2.31 | 1.7 | 29.43 | 15.7 | 17.35 | 263323 | 231341 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AL | SA197AL | sa19 7al | sa197al | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 516 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 265742 | 225125 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AN | SA197AN | sa19 7an | sa197an | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 1037 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 265357 | 225506 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AP | SA197AP | sa19 7ap | sa197ap | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 1661 | 1344 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.05 | 13.36 | 14.77 | 265830 | 226549 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AQ | SA197AQ | sa19 7aq | sa197aq | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 818 | 1563 | Over1500 | 3.13 | 2.29 | 1.68 | 29.13 | 15.54 | 17.17 | 263336 | 232180 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AR | SA197AR | sa19 7ar | sa197ar | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 2112 | 1344 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.05 | 13.36 | 14.77 | 265756 | 226995 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AS | SA197AS | sa19 7as | sa197as | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 2359 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 265093 | 227006 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AT | SA197AT | sa19 7at | sa197at | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 1646 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 265195 | 226221 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AU | SA197AU | sa19 7au | sa197au | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 410 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 265861 | 225130 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AW | SA197AW | sa19 7aw | sa197aw | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 733 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 265898 | 225592 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AX | SA197AX | sa19 7ax | sa197ax | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1283 | 1544 | Over1500 | 3.09 | 2.26 | 1.66 | 28.78 | 15.35 | 16.96 | 263191 | 232735 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AY | SA197AY | sa19 7ay | sa197ay | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 1715 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 266781 | 226556 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7AZ | SA197AZ | sa19 7az | sa197az | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 2544 | 1603 | Over1500 | 3.21 | 2.35 | 1.72 | 29.88 | 15.93 | 17.61 | 261977 | 233631 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BA | SA197BA | sa19 7ba | sa197ba | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 1798 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 267270 | 226737 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BB | SA197BB | sa19 7bb | sa197bb | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 2148 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 267362 | 227173 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BD | SA197BD | sa19 7bd | sa197bd | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 2775 | 1379 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.7 | 13.71 | 15.15 | 266344 | 227707 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BE | SA197BE | sa19 7be | sa197be | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2734 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 267157 | 228180 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BG | SA197BG | sa19 7bg | sa197bg | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 1559 | 1305 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.32 | 12.97 | 14.34 | 267520 | 226599 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BH | SA197BH | sa19 7bh | sa197bh | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 1336 | 1362 | 1200to1500 | 2.73 | 1.99 | 1.46 | 25.39 | 13.54 | 14.96 | 267853 | 226484 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BJ | SA197BJ | sa19 7bj | sa197bj | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 2205 | 1535 | Over1500 | 3.07 | 2.25 | 1.65 | 28.61 | 15.26 | 16.86 | 262561 | 233942 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BL | SA197BL | sa19 7bl | sa197bl | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 1924 | 1305 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.32 | 12.97 | 14.34 | 267737 | 227060 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BN | SA197BN | sa19 7bn | sa197bn | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1177 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 268718 | 228030 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BP | SA197BP | sa19 7bp | sa197bp | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 1558 | 1305 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.32 | 12.97 | 14.34 | 268207 | 226748 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BQ | SA197BQ | sa19 7bq | sa197bq | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 2595 | 1630 | Over1500 | 3.26 | 2.39 | 1.75 | 30.38 | 16.2 | 17.91 | 260838 | 232363 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BR | SA197BR | sa19 7br | sa197br | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 1597 | 1305 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.32 | 12.97 | 14.34 | 267774 | 226733 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BS | SA197BS | sa19 7bs | sa197bs | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 972 | 1364 | 1200to1500 | 2.73 | 2 | 1.46 | 25.42 | 13.56 | 14.99 | 266543 | 225852 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BT | SA197BT | sa19 7bt | sa197bt | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 782 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 265965 | 225673 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BU | SA197BU | sa19 7bu | sa197bu | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 612 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 265946 | 225481 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BW | SA197BW | sa19 7bw | sa197bw | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1031 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 268879 | 227940 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BX | SA197BX | sa19 7bx | sa197bx | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 1991 | 1535 | Over1500 | 3.07 | 2.25 | 1.65 | 28.61 | 15.26 | 16.86 | 263360 | 234399 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BY | SA197BY | sa19 7by | sa197by | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2197 | 1410 | 1200to1500 | 2.82 | 2.07 | 1.51 | 26.28 | 14.02 | 15.49 | 264316 | 226694 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7BZ | SA197BZ | sa19 7bz | sa197bz | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 2583 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 264293 | 234388 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DA | SA197DA | sa19 7da | sa197da | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 3098 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 265126 | 227832 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DD | SA197DD | sa19 7dd | sa197dd | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 3433 | 1393 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.96 | 13.85 | 15.3 | 265679 | 228761 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DE | SA197DE | sa19 7de | sa197de | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 3541 | 1379 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.7 | 13.71 | 15.15 | 266096 | 228473 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DF | SA197DF | sa19 7df | sa197df | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3408 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 266565 | 228885 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DG | SA197DG | sa19 7dg | sa197dg | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2984 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 267153 | 229328 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DH | SA197DH | sa19 7dh | sa197dh | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3070 | 1401 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.11 | 13.93 | 15.39 | 267783 | 230372 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DJ | SA197DJ | sa19 7dj | sa197dj | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 3109 | 1499 | 1200to1500 | 3 | 2.2 | 1.61 | 27.94 | 14.9 | 16.47 | 265833 | 234328 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DL | SA197DL | sa19 7dl | sa197dl | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 3262 | 1460 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.21 | 14.51 | 16.04 | 267148 | 230764 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DN | SA197DN | sa19 7dn | sa197dn | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2694 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 266259 | 230241 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DP | SA197DP | sa19 7dp | sa197dp | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2956 | 1393 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.96 | 13.85 | 15.3 | 265781 | 229387 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DQ | SA197DQ | sa19 7dq | sa197dq | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 2774 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 264789 | 234740 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DR | SA197DR | sa19 7dr | sa197dr | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1003 | 1524 | Over1500 | 3.05 | 2.23 | 1.64 | 28.4 | 15.15 | 16.74 | 264314 | 230815 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DS | SA197DS | sa19 7ds | sa197ds | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 470 | 1524 | Over1500 | 3.05 | 2.23 | 1.64 | 28.4 | 15.15 | 16.74 | 264010 | 231314 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DT | SA197DT | sa19 7dt | sa197dt | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1060 | 1524 | Over1500 | 3.05 | 2.23 | 1.64 | 28.4 | 15.15 | 16.74 | 263570 | 230837 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DU | SA197DU | sa19 7du | sa197du | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1810 | 1569 | Over1500 | 3.14 | 2.3 | 1.69 | 29.24 | 15.6 | 17.24 | 262832 | 230443 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DW | SA197DW | sa19 7dw | sa197dw | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 3306 | 1393 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.96 | 13.85 | 15.3 | 266378 | 229435 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DX | SA197DX | sa19 7dx | sa197dx | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 3093 | 1499 | 1200to1500 | 3 | 2.2 | 1.61 | 27.94 | 14.9 | 16.47 | 266111 | 234088 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DY | SA197DY | sa19 7dy | sa197dy | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1631 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 263536 | 230234 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7DZ | SA197DZ | sa19 7dz | sa197dz | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2808 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 266324 | 233428 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EA | SA197EA | sa19 7ea | sa197ea | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1940 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 264270 | 229855 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EB | SA197EB | sa19 7eb | sa197eb | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1754 | 1569 | Over1500 | 3.14 | 2.3 | 1.69 | 29.24 | 15.6 | 17.24 | 263434 | 230140 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7ED | SA197ED | sa19 7ed | sa197ed | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2205 | 1569 | Over1500 | 3.14 | 2.3 | 1.69 | 29.24 | 15.6 | 17.24 | 262635 | 230092 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EE | SA197EE | sa19 7ee | sa197ee | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2236 | 1587 | Over1500 | 3.18 | 2.32 | 1.7 | 29.58 | 15.78 | 17.44 | 261913 | 231125 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EF | SA197EF | sa19 7ef | sa197ef | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2716 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 262426 | 229606 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EG | SA197EG | sa19 7eg | sa197eg | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2862 | 1587 | Over1500 | 3.18 | 2.32 | 1.7 | 29.58 | 15.78 | 17.44 | 262304 | 229496 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EH | SA197EH | sa19 7eh | sa197eh | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 3318 | 1614 | Over1500 | 3.23 | 2.36 | 1.73 | 30.08 | 16.04 | 17.73 | 261333 | 229879 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EJ | SA197EJ | sa19 7ej | sa197ej | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1136 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 265129 | 232136 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EL | SA197EL | sa19 7el | sa197el | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2817 | 1631 | Over1500 | 3.26 | 2.39 | 1.75 | 30.4 | 16.21 | 17.92 | 261382 | 229358 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EN | SA197EN | sa19 7en | sa197en | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 3160 | 1614 | Over1500 | 3.23 | 2.36 | 1.73 | 30.08 | 16.04 | 17.73 | 260850 | 229533 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EP | SA197EP | sa19 7ep | sa197ep | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 3541 | 1653 | Over1500 | 3.31 | 2.42 | 1.78 | 30.81 | 16.43 | 18.16 | 260327 | 229693 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EQ | SA197EQ | sa19 7eq | sa197eq | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1897 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 265789 | 232539 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7ER | SA197ER | sa19 7er | sa197er | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 3437 | 1640 | Over1500 | 3.28 | 2.4 | 1.76 | 30.57 | 16.3 | 18.02 | 259413 | 228757 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7ES | SA197ES | sa19 7es | sa197es | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2569 | 1643 | Over1500 | 3.29 | 2.41 | 1.76 | 30.62 | 16.33 | 18.05 | 260422 | 228567 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7ET | SA197ET | sa19 7et | sa197et | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1728 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 260966 | 227926 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EU | SA197EU | sa19 7eu | sa197eu | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1759 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 260827 | 227832 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EW | SA197EW | sa19 7ew | sa197ew | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2717 | 1631 | Over1500 | 3.26 | 2.39 | 1.75 | 30.4 | 16.21 | 17.92 | 261174 | 229186 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EX | SA197EX | sa19 7ex | sa197ex | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2107 | 1555 | Over1500 | 3.11 | 2.28 | 1.67 | 28.98 | 15.46 | 17.08 | 266157 | 231793 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EY | SA197EY | sa19 7ey | sa197ey | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2362 | 1555 | Over1500 | 3.11 | 2.28 | 1.67 | 28.98 | 15.46 | 17.08 | 266379 | 232174 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7EZ | SA197EZ | sa19 7ez | sa197ez | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2665 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 266600 | 232554 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HA | SA197HA | sa19 7ha | sa197ha | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1833 | 1560 | Over1500 | 3.12 | 2.28 | 1.68 | 29.08 | 15.51 | 17.14 | 260471 | 227439 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HB | SA197HB | sa19 7hb | sa197hb | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1547 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 260823 | 227483 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HD | SA197HD | sa19 7hd | sa197hd | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1376 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 260939 | 227345 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HE | SA197HE | sa19 7he | sa197he | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1623 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 260588 | 227174 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HF | SA197HF | sa19 7hf | sa197hf | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 953 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 261186 | 226830 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HG | SA197HG | sa19 7hg | sa197hg | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 431 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 261782 | 226907 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HJ | SA197HJ | sa19 7hj | sa197hj | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2773 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263346 | 223316 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HN | SA197HN | sa19 7hn | sa197hn | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2971 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263442 | 223493 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HP | SA197HP | sa19 7hp | sa197hp | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2749 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263316 | 223309 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HR | SA197HR | sa19 7hr | sa197hr | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2683 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263205 | 223312 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HS | SA197HS | sa19 7hs | sa197hs | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2964 | 1428 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.62 | 14.2 | 15.69 | 263288 | 223599 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HT | SA197HT | sa19 7ht | sa197ht | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 3091 | 1428 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.62 | 14.2 | 15.69 | 263283 | 223755 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HU | SA197HU | sa19 7hu | sa197hu | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2873 | 1428 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.62 | 14.2 | 15.69 | 263334 | 224037 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HW | SA197HW | sa19 7hw | sa197hw | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2303 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 263026 | 222970 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HY | SA197HY | sa19 7hy | sa197hy | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2422 | 1428 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.62 | 14.2 | 15.69 | 263198 | 224472 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7HZ | SA197HZ | sa19 7hz | sa197hz | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 1643 | 1563 | Over1500 | 3.13 | 2.29 | 1.68 | 29.13 | 15.54 | 17.17 | 263172 | 234693 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JA | SA197JA | sa19 7ja | sa197ja | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 2248 | 1648 | Over1500 | 3.3 | 2.41 | 1.77 | 30.72 | 16.38 | 18.11 | 261383 | 234133 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JB | SA197JB | sa19 7jb | sa197jb | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 536 | 1562 | Over1500 | 3.13 | 2.29 | 1.68 | 29.11 | 15.53 | 17.16 | 262526 | 235620 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JD | SA197JD | sa19 7jd | sa197jd | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 392 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 262003 | 236139 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JE | SA197JE | sa19 7je | sa197je | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 507 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 261896 | 236228 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JF | SA197JF | sa19 7jf | sa197jf | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 497 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 261914 | 236266 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JG | SA197JG | sa19 7jg | sa197jg | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 445 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 261964 | 236249 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JH | SA197JH | sa19 7jh | sa197jh | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 450 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 261978 | 236308 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JJ | SA197JJ | sa19 7jj | sa197jj | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 429 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 262037 | 236376 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JL | SA197JL | sa19 7jl | sa197jl | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 449 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 262036 | 236410 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JN | SA197JN | sa19 7jn | sa197jn | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 517 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 262042 | 236517 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JP | SA197JP | sa19 7jp | sa197jp | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 456 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 262067 | 236456 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JQ | SA197JQ | sa19 7jq | sa197jq | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 424 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 261991 | 236267 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JR | SA197JR | sa19 7jr | sa197jr | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 390 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 262141 | 236436 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JS | SA197JS | sa19 7js | sa197js | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 332 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 262189 | 236400 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JT | SA197JT | sa19 7jt | sa197jt | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 1134 | 1493 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.83 | 14.84 | 16.4 | 263231 | 236906 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JU | SA197JU | sa19 7ju | sa197ju | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1694 | 1539 | Over1500 | 3.08 | 2.25 | 1.65 | 28.68 | 15.3 | 16.91 | 263943 | 237186 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JW | SA197JW | sa19 7jw | sa197jw | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 576 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 262024 | 236581 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JX | SA197JX | sa19 7jx | sa197jx | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1383 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 264220 | 237872 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JY | SA197JY | sa19 7jy | sa197jy | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1882 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 263794 | 238212 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7JZ | SA197JZ | sa19 7jz | sa197jz | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 884 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 261837 | 236826 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LA | SA197LA | sa19 7la | sa197la | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2019 | 1436 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.76 | 14.27 | 15.78 | 262740 | 224719 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LB | SA197LB | sa19 7lb | sa197lb | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2515 | 1428 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.62 | 14.2 | 15.69 | 262698 | 224193 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LD | SA197LD | sa19 7ld | sa197ld | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2455 | 1414 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.35 | 14.06 | 15.54 | 263688 | 224752 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LE | SA197LE | sa19 7le | sa197le | Carmarthenshire | Sir Gaerfyrddin | Cwm Ifor WwTW | 2173 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 264375 | 226079 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LF | SA197LF | sa19 7lf | sa197lf | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2252 | 1414 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.35 | 14.06 | 15.54 | 263612 | 224954 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LG | SA197LG | sa19 7lg | sa197lg | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2107 | 1414 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.35 | 14.06 | 15.54 | 263661 | 225204 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LH | SA197LH | sa19 7lh | sa197lh | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1601 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 263514 | 225854 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LJ | SA197LJ | sa19 7lj | sa197lj | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 721 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 261675 | 236111 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LL | SA197LL | sa19 7ll | sa197ll | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1605 | 1472 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.44 | 14.63 | 16.17 | 263265 | 225515 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LN | SA197LN | sa19 7ln | sa197ln | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1952 | 1436 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.76 | 14.27 | 15.78 | 263382 | 225151 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LP | SA197LP | sa19 7lp | sa197lp | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1013 | 1517 | Over1500 | 3.04 | 2.22 | 1.63 | 28.27 | 15.08 | 16.67 | 262488 | 225696 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LQ | SA197LQ | sa19 7lq | sa197lq | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 1905 | 1483 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.64 | 14.74 | 16.29 | 261807 | 237952 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LR | SA197LR | sa19 7lr | sa197lr | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1923 | 1488 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.73 | 14.79 | 16.35 | 261994 | 224721 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LS | SA197LS | sa19 7ls | sa197ls | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2108 | 1488 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.73 | 14.79 | 16.35 | 262350 | 224545 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LT | SA197LT | sa19 7lt | sa197lt | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 513 | 1517 | Over1500 | 3.04 | 2.22 | 1.63 | 28.27 | 15.08 | 16.67 | 262317 | 226166 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LU | SA197LU | sa19 7lu | sa197lu | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 617 | 1472 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.44 | 14.63 | 16.17 | 262625 | 226286 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LW | SA197LW | sa19 7lw | sa197lw | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1056 | 1472 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.44 | 14.63 | 16.17 | 262600 | 225700 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LX | SA197LX | sa19 7lx | sa197lx | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 1319 | 1595 | Over1500 | 3.19 | 2.34 | 1.71 | 29.73 | 15.86 | 17.52 | 261081 | 236025 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LY | SA197LY | sa19 7ly | sa197ly | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 208 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 262299 | 226534 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7LZ | SA197LZ | sa19 7lz | sa197lz | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 2092 | 1576 | Over1500 | 3.15 | 2.31 | 1.69 | 29.37 | 15.67 | 17.32 | 260323 | 235855 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NA | SA197NA | sa19 7na | sa197na | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 834 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 261600 | 227292 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NB | SA197NB | sa19 7nb | sa197nb | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 447 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 262167 | 227084 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7ND | SA197ND | sa19 7nd | sa197nd | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 967 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 262196 | 227604 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NE | SA197NE | sa19 7ne | sa197ne | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1376 | 1486 | 1200to1500 | 2.97 | 2.18 | 1.6 | 27.7 | 14.77 | 16.33 | 263359 | 227237 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NF | SA197NF | sa19 7nf | sa197nf | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1409 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 263519 | 226477 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NG | SA197NG | sa19 7ng | sa197ng | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1480 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 263563 | 226313 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NH | SA197NH | sa19 7nh | sa197nh | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1610 | 1486 | 1200to1500 | 2.97 | 2.18 | 1.6 | 27.7 | 14.77 | 16.33 | 263481 | 227499 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NJ | SA197NJ | sa19 7nj | sa197nj | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 1951 | 1636 | Over1500 | 3.27 | 2.4 | 1.76 | 30.49 | 16.26 | 17.97 | 260011 | 235208 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NL | SA197NL | sa19 7nl | sa197nl | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2405 | 1456 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.14 | 14.47 | 16 | 264060 | 228060 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NN | SA197NN | sa19 7nn | sa197nn | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2042 | 1456 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.14 | 14.47 | 16 | 263564 | 228084 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NP | SA197NP | sa19 7np | sa197np | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1455 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 261928 | 228082 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NQ | SA197NQ | sa19 7nq | sa197nq | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 2217 | 1636 | Over1500 | 3.27 | 2.4 | 1.76 | 30.49 | 16.26 | 17.97 | 260380 | 235217 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NR | SA197NR | sa19 7nr | sa197nr | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1682 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 261378 | 228149 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NS | SA197NS | sa19 7ns | sa197ns | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1834 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 261969 | 228467 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NT | SA197NT | sa19 7nt | sa197nt | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1832 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 262027 | 228469 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NU | SA197NU | sa19 7nu | sa197nu | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2398 | 1578 | Over1500 | 3.16 | 2.31 | 1.69 | 29.41 | 15.69 | 17.34 | 262582 | 228993 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NW | SA197NW | sa19 7nw | sa197nw | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2718 | 1578 | Over1500 | 3.16 | 2.31 | 1.69 | 29.41 | 15.69 | 17.34 | 263205 | 229199 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NX | SA197NX | sa19 7nx | sa197nx | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 2028 | 1636 | Over1500 | 3.27 | 2.4 | 1.76 | 30.49 | 16.26 | 17.97 | 260385 | 234874 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NY | SA197NY | sa19 7ny | sa197ny | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1536 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 262049 | 228174 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7NZ | SA197NZ | sa19 7nz | sa197nz | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 1751 | 1636 | Over1500 | 3.27 | 2.4 | 1.76 | 30.49 | 16.26 | 17.97 | 260169 | 234696 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PA | SA197PA | sa19 7pa | sa197pa | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 436 | 1517 | Over1500 | 3.04 | 2.22 | 1.63 | 28.27 | 15.08 | 16.67 | 262413 | 226317 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PE | SA197PE | sa19 7pe | sa197pe | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 1389 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 261188 | 236827 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PF | SA197PF | sa19 7pf | sa197pf | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 1686 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 260749 | 236503 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PG | SA197PG | sa19 7pg | sa197pg | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 2519 | 1518 | Over1500 | 3.04 | 2.22 | 1.63 | 28.29 | 15.09 | 16.68 | 259925 | 236631 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PH | SA197PH | sa19 7ph | sa197ph | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 2173 | 1635 | Over1500 | 3.27 | 2.39 | 1.76 | 30.47 | 16.25 | 17.96 | 259216 | 237630 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PL | SA197PL | sa19 7pl | sa197pl | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 1305 | 1666 | Over1500 | 3.33 | 2.44 | 1.79 | 31.05 | 16.56 | 18.3 | 257932 | 237722 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PN | SA197PN | sa19 7pn | sa197pn | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 1510 | 1635 | Over1500 | 3.27 | 2.39 | 1.76 | 30.47 | 16.25 | 17.96 | 258710 | 238061 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PP | SA197PP | sa19 7pp | sa197pp | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 423 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 257866 | 238757 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PQ | SA197PQ | sa19 7pq | sa197pq | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 1239 | 1562 | Over1500 | 3.13 | 2.29 | 1.68 | 29.11 | 15.53 | 17.16 | 263487 | 235556 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PR | SA197PR | sa19 7pr | sa197pr | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 406 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 257764 | 238651 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PS | SA197PS | sa19 7ps | sa197ps | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 312 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 257785 | 238849 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PT | SA197PT | sa19 7pt | sa197pt | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 425 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 257624 | 239353 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PU | SA197PU | sa19 7pu | sa197pu | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 53 | 1639 | Over1500 | 3.28 | 2.4 | 1.76 | 30.55 | 16.29 | 18.01 | 257441 | 238971 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PW | SA197PW | sa19 7pw | sa197pw | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 728 | 1666 | Over1500 | 3.33 | 2.44 | 1.79 | 31.05 | 16.56 | 18.3 | 257879 | 238335 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7PY | SA197PY | sa19 7py | sa197py | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 624 | 1639 | Over1500 | 3.28 | 2.4 | 1.76 | 30.55 | 16.29 | 18.01 | 257162 | 239481 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RA | SA197RA | sa19 7ra | sa197ra | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 1293 | 1618 | Over1500 | 3.24 | 2.37 | 1.74 | 30.16 | 16.08 | 17.78 | 256835 | 237835 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RB | SA197RB | sa19 7rb | sa197rb | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 1490 | 1653 | Over1500 | 3.31 | 2.42 | 1.78 | 30.81 | 16.43 | 18.16 | 256061 | 239370 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RD | SA197RD | sa19 7rd | sa197rd | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 3466 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 254039 | 238633 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RE | SA197RE | sa19 7re | sa197re | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 1966 | 1612 | Over1500 | 3.23 | 2.36 | 1.73 | 30.05 | 16.02 | 17.71 | 256063 | 240302 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RF | SA197RF | sa19 7rf | sa197rf | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 2874 | 1570 | Over1500 | 3.14 | 2.3 | 1.69 | 29.26 | 15.61 | 17.25 | 257698 | 241816 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RG | SA197RG | sa19 7rg | sa197rg | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 1419 | 1626 | Over1500 | 3.25 | 2.38 | 1.75 | 30.31 | 16.16 | 17.86 | 257084 | 240309 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RH | SA197RH | sa19 7rh | sa197rh | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 821 | 1611 | Over1500 | 3.22 | 2.36 | 1.73 | 30.03 | 16.01 | 17.7 | 257860 | 239683 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RL | SA197RL | sa19 7rl | sa197rl | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 1465 | 1611 | Over1500 | 3.22 | 2.36 | 1.73 | 30.03 | 16.01 | 17.7 | 258389 | 240106 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RN | SA197RN | sa19 7rn | sa197rn | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 1366 | 1634 | Over1500 | 3.27 | 2.39 | 1.75 | 30.46 | 16.24 | 17.95 | 258787 | 239379 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RP | SA197RP | sa19 7rp | sa197rp | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 2248 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 259006 | 240609 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RR | SA197RR | sa19 7rr | sa197rr | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 2692 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 259265 | 240973 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RS | SA197RS | sa19 7rs | sa197rs | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 2917 | 1635 | Over1500 | 3.27 | 2.39 | 1.76 | 30.47 | 16.25 | 17.96 | 260204 | 240017 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RT | SA197RT | sa19 7rt | sa197rt | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 3362 | 1576 | Over1500 | 3.15 | 2.31 | 1.69 | 29.37 | 15.67 | 17.32 | 260601 | 240224 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RU | SA197RU | sa19 7ru | sa197ru | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 3516 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 260471 | 240813 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RW | SA197RW | sa19 7rw | sa197rw | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 2062 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 259344 | 239851 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7RY | SA197RY | sa19 7ry | sa197ry | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 3510 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 260262 | 241103 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SA | SA197SA | sa19 7sa | sa197sa | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 2917 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 259760 | 240781 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SB | SA197SB | sa19 7sb | sa197sb | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 3786 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 260098 | 241694 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SD | SA197SD | sa19 7sd | sa197sd | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 3821 | 1624 | Over1500 | 3.25 | 2.38 | 1.74 | 30.27 | 16.14 | 17.84 | 260972 | 240522 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SE | SA197SE | sa19 7se | sa197se | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 4013 | 1624 | Over1500 | 3.25 | 2.38 | 1.74 | 30.27 | 16.14 | 17.84 | 261141 | 240969 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SF | SA197SF | sa19 7sf | sa197sf | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 3797 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 260216 | 242261 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SG | SA197SG | sa19 7sg | sa197sg | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 3722 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 261995 | 240825 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SH | SA197SH | sa19 7sh | sa197sh | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 4121 | 1576 | Over1500 | 3.15 | 2.31 | 1.69 | 29.37 | 15.67 | 17.32 | 261420 | 240187 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SL | SA197SL | sa19 7sl | sa197sl | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 3416 | 1576 | Over1500 | 3.15 | 2.31 | 1.69 | 29.37 | 15.67 | 17.32 | 260818 | 239719 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SN | SA197SN | sa19 7sn | sa197sn | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 3039 | 1517 | Over1500 | 3.04 | 2.22 | 1.63 | 28.27 | 15.08 | 16.67 | 261664 | 239089 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SP | SA197SP | sa19 7sp | sa197sp | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 253 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 257743 | 238965 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7ST | SA197ST | sa19 7st | sa197st | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 2678 | 1452 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.06 | 14.43 | 15.95 | 261835 | 223836 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SU | SA197SU | sa19 7su | sa197su | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2650 | 1452 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.06 | 14.43 | 15.95 | 261533 | 224056 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SW | SA197SW | sa19 7sw | sa197sw | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 2452 | 1544 | Over1500 | 3.09 | 2.26 | 1.66 | 28.78 | 15.35 | 16.96 | 261458 | 238406 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7SY | SA197SY | sa19 7sy | sa197sy | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2513 | 1468 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.36 | 14.59 | 16.13 | 260973 | 224405 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TA | SA197TA | sa19 7ta | sa197ta | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2558 | 1452 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.06 | 14.43 | 15.95 | 261678 | 224121 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TB | SA197TB | sa19 7tb | sa197tb | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1687 | 1485 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.68 | 14.76 | 16.32 | 261184 | 225237 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TD | SA197TD | sa19 7td | sa197td | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1965 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 260259 | 226009 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TE | SA197TE | sa19 7te | sa197te | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2247 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 260019 | 225843 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TF | SA197TF | sa19 7tf | sa197tf | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2831 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 259332 | 226151 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TG | SA197TG | sa19 7tg | sa197tg | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 3126 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 259004 | 226880 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TL | SA197TL | sa19 7tl | sa197tl | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 3784 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 258345 | 226887 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TN | SA197TN | sa19 7tn | sa197tn | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 3909 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 258213 | 226731 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TP | SA197TP | sa19 7tp | sa197tp | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2897 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 259252 | 227045 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TR | SA197TR | sa19 7tr | sa197tr | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2645 | 1599 | Over1500 | 3.2 | 2.34 | 1.72 | 29.8 | 15.89 | 17.57 | 259856 | 228006 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TS | SA197TS | sa19 7ts | sa197ts | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2061 | 1560 | Over1500 | 3.12 | 2.28 | 1.68 | 29.08 | 15.51 | 17.14 | 260085 | 226965 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TT | SA197TT | sa19 7tt | sa197tt | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1769 | 1560 | Over1500 | 3.12 | 2.28 | 1.68 | 29.08 | 15.51 | 17.14 | 260376 | 226935 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TU | SA197TU | sa19 7tu | sa197tu | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2191 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 259936 | 226471 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TW | SA197TW | sa19 7tw | sa197tw | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 3902 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 258319 | 227518 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7TY | SA197TY | sa19 7ty | sa197ty | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2785 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 259527 | 225626 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7UA | SA197UA | sa19 7ua | sa197ua | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 3328 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 258874 | 225910 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7UB | SA197UB | sa19 7ub | sa197ub | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 3215 | 1497 | 1200to1500 | 3 | 2.19 | 1.61 | 27.9 | 14.88 | 16.45 | 259164 | 225376 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7UD | SA197UD | sa19 7ud | sa197ud | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 3307 | 1497 | 1200to1500 | 3 | 2.19 | 1.61 | 27.9 | 14.88 | 16.45 | 258725 | 225450 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7UE | SA197UE | sa19 7ue | sa197ue | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 3592 | 1558 | Over1500 | 3.12 | 2.28 | 1.67 | 29.04 | 15.49 | 17.12 | 258233 | 225873 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7UF | SA197UF | sa19 7uf | sa197uf | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 3624 | 1558 | Over1500 | 3.12 | 2.28 | 1.67 | 29.04 | 15.49 | 17.12 | 257676 | 225959 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7UG | SA197UG | sa19 7ug | sa197ug | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 4254 | 1561 | Over1500 | 3.12 | 2.29 | 1.68 | 29.09 | 15.52 | 17.15 | 257557 | 226589 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7UH | SA197UH | sa19 7uh | sa197uh | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 3725 | 1515 | Over1500 | 3.03 | 2.22 | 1.63 | 28.24 | 15.06 | 16.65 | 256961 | 226186 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7UL | SA197UL | sa19 7ul | sa197ul | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 3899 | 1558 | Over1500 | 3.12 | 2.28 | 1.67 | 29.04 | 15.49 | 17.12 | 258245 | 226214 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7UR | SA197UR | sa19 7ur | sa197ur | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 1627 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 263641 | 226063 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7US | SA197US | sa19 7us | sa197us | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 2517 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 264556 | 227272 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7UT | SA197UT | sa19 7ut | sa197ut | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2986 | 1447 | 1200to1500 | 2.9 | 2.12 | 1.55 | 26.97 | 14.38 | 15.9 | 265228 | 229039 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7UU | SA197UU | sa19 7uu | sa197uu | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2286 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 265664 | 230164 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7UY | SA197UY | sa19 7uy | sa197uy | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1976 | 1493 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.83 | 14.84 | 16.4 | 264860 | 229980 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7XZ | SA197XZ | sa19 7xz | sa197xz | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 918 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 263634 | 232600 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YA | SA197YA | sa19 7ya | sa197ya | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1302 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 264786 | 230708 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YB | SA197YB | sa19 7yb | sa197yb | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1399 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 265221 | 231017 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YD | SA197YD | sa19 7yd | sa197yd | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1626 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 265566 | 231195 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YE | SA197YE | sa19 7ye | sa197ye | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2273 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 265945 | 230527 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YF | SA197YF | sa19 7yf | sa197yf | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1181 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 264760 | 230838 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YG | SA197YG | sa19 7yg | sa197yg | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 459 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 264508 | 231814 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YH | SA197YH | sa19 7yh | sa197yh | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 561 | 1521 | Over1500 | 3.04 | 2.23 | 1.63 | 28.35 | 15.12 | 16.71 | 264067 | 232343 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YL | SA197YL | sa19 7yl | sa197yl | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 871 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 263991 | 232651 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YN | SA197YN | sa19 7yn | sa197yn | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1449 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 264028 | 233231 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YP | SA197YP | sa19 7yp | sa197yp | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 920 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 263709 | 232636 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YR | SA197YR | sa19 7yr | sa197yr | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1064 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 263649 | 232767 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YS | SA197YS | sa19 7ys | sa197ys | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1304 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 263519 | 232973 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YT | SA197YT | sa19 7yt | sa197yt | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2054 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 263501 | 233761 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YU | SA197YU | sa19 7yu | sa197yu | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2080 | 1534 | Over1500 | 3.07 | 2.25 | 1.65 | 28.59 | 15.25 | 16.85 | 264529 | 233806 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YW | SA197YW | sa19 7yw | sa197yw | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1936 | 1519 | Over1500 | 3.04 | 2.22 | 1.63 | 28.31 | 15.1 | 16.69 | 265244 | 233306 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 7YY | SA197YY | sa19 7yy | sa197yy | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 1146 | 1544 | Over1500 | 3.09 | 2.26 | 1.66 | 28.78 | 15.35 | 16.96 | 263328 | 232672 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AA | SA198AA | sa19 8aa | sa198aa | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3832 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 271254 | 231720 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AB | SA198AB | sa19 8ab | sa198ab | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 4027 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 271165 | 231959 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AD | SA198AD | sa19 8ad | sa198ad | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 4057 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 271227 | 231970 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AE | SA198AE | sa19 8ae | sa198ae | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 4153 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 271133 | 232102 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AF | SA198AF | sa19 8af | sa198af | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3776 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 271281 | 231650 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AG | SA198AG | sa19 8ag | sa198ag | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 4083 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 271135 | 232028 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AH | SA198AH | sa19 8ah | sa198ah | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 4898 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 270724 | 232966 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AJ | SA198AJ | sa19 8aj | sa198aj | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1127 | 1557 | Over1500 | 3.12 | 2.28 | 1.67 | 29.02 | 15.48 | 17.11 | 265017 | 243444 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AL | SA198AL | sa19 8al | sa198al | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 4717 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 270910 | 232744 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AN | SA198AN | sa19 8an | sa198an | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 5074 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 271058 | 233277 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AP | SA198AP | sa19 8ap | sa198ap | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 4479 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 272026 | 234973 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AQ | SA198AQ | sa19 8aq | sa198aq | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 2085 | 1518 | Over1500 | 3.04 | 2.22 | 1.63 | 28.29 | 15.09 | 16.68 | 264815 | 242465 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AR | SA198AR | sa19 8ar | sa198ar | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 5691 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 270627 | 234628 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AS | SA198AS | sa19 8as | sa198as | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 5391 | 1475 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.49 | 14.66 | 16.21 | 270842 | 234221 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AT | SA198AT | sa19 8at | sa198at | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1796 | 1543 | Over1500 | 3.09 | 2.26 | 1.66 | 28.76 | 15.34 | 16.95 | 263947 | 246130 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AU | SA198AU | sa19 8au | sa198au | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3899 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 271175 | 231820 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AW | SA198AW | sa19 8aw | sa198aw | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 4510 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 271693 | 233981 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AX | SA198AX | sa19 8ax | sa198ax | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1523 | 1557 | Over1500 | 3.12 | 2.28 | 1.67 | 29.02 | 15.48 | 17.11 | 265341 | 243127 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AY | SA198AY | sa19 8ay | sa198ay | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 5767 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 270241 | 233895 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8AZ | SA198AZ | sa19 8az | sa198az | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1557 | 1550 | Over1500 | 3.1 | 2.27 | 1.66 | 28.89 | 15.41 | 17.03 | 266242 | 243964 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BA | SA198BA | sa19 8ba | sa198ba | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 5406 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 269803 | 234246 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BB | SA198BB | sa19 8bb | sa198bb | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 5187 | 1500 |  | 3 | 2.2 | 1.61 | 27.96 | 14.91 | 16.48 | 269925 | 234788 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BD | SA198BD | sa19 8bd | sa198bd | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 3745 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 268325 | 235074 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BG | SA198BG | sa19 8bg | sa198bg | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 3930 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 269731 | 236366 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BH | SA198BH | sa19 8bh | sa198bh | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 3634 | 1548 | Over1500 | 3.1 | 2.27 | 1.66 | 28.85 | 15.39 | 17.01 | 269772 | 236765 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BJ | SA198BJ | sa19 8bj | sa198bj | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 1138 | 1469 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.38 | 14.6 | 16.14 | 264826 | 240065 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BL | SA198BL | sa19 8bl | sa198bl | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 3037 | 1509 | Over1500 | 3.02 | 2.21 | 1.62 | 28.13 | 15 | 16.58 | 268219 | 236118 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BN | SA198BN | sa19 8bn | sa198bn | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 3074 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 267519 | 235235 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BP | SA198BP | sa19 8bp | sa198bp | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 3692 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 268864 | 235934 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BQ | SA198BQ | sa19 8bq | sa198bq | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 1613 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 265588 | 242149 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BR | SA198BR | sa19 8br | sa198br | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 4103 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 269237 | 235761 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BS | SA198BS | sa19 8bs | sa198bs | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 5278 | 1500 |  | 3 | 2.2 | 1.61 | 27.96 | 14.91 | 16.48 | 270236 | 235088 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BW | SA198BW | sa19 8bw | sa198bw | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 3392 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 268103 | 235354 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BX | SA198BX | sa19 8bx | sa198bx | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 2008 | 1491 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.79 | 14.82 | 16.38 | 264221 | 239098 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8BY | SA198BY | sa19 8by | sa198by | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 5395 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 269928 | 233534 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DA | SA198DA | sa19 8da | sa198da | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 5105 | 1500 |  | 3 | 2.2 | 1.61 | 27.96 | 14.91 | 16.48 | 270068 | 235189 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DB | SA198DB | sa19 8db | sa198db | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 3386 | 1552 | Over1500 | 3.11 | 2.27 | 1.67 | 28.93 | 15.43 | 17.05 | 269401 | 236799 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DD | SA198DD | sa19 8dd | sa198dd | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 3040 | 1552 | Over1500 | 3.11 | 2.27 | 1.67 | 28.93 | 15.43 | 17.05 | 269240 | 237108 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DE | SA198DE | sa19 8de | sa198de | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 2872 | 1584 | Over1500 | 3.17 | 2.32 | 1.7 | 29.52 | 15.75 | 17.4 | 269594 | 237635 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DF | SA198DF | sa19 8df | sa198df | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 3945 | 1619 | Over1500 | 3.24 | 2.37 | 1.74 | 30.18 | 16.09 | 17.79 | 270963 | 237711 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DG | SA198DG | sa19 8dg | sa198dg | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 3897 | 1570 | Over1500 | 3.14 | 2.3 | 1.69 | 29.26 | 15.61 | 17.25 | 271827 | 238196 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DH | SA198DH | sa19 8dh | sa198dh | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 4178 | 1570 | Over1500 | 3.14 | 2.3 | 1.69 | 29.26 | 15.61 | 17.25 | 271826 | 237551 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DJ | SA198DJ | sa19 8dj | sa198dj | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 1572 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 264449 | 241269 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DL | SA198DL | sa19 8dl | sa198dl | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 3529 | 1554 | Over1500 | 3.11 | 2.28 | 1.67 | 28.96 | 15.45 | 17.07 | 272523 | 237658 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DN | SA198DN | sa19 8dn | sa198dn | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 4149 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 272195 | 237057 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DP | SA198DP | sa19 8dp | sa198dp | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 2226 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 264289 | 242189 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DQ | SA198DQ | sa19 8dq | sa198dq | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 2148 | 1487 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.72 | 14.78 | 16.34 | 263845 | 239790 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DR | SA198DR | sa19 8dr | sa198dr | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1818 | 1557 | Over1500 | 3.12 | 2.28 | 1.67 | 29.02 | 15.48 | 17.11 | 264520 | 242754 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DS | SA198DS | sa19 8ds | sa198ds | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 1192 | 1524 | Over1500 | 3.05 | 2.23 | 1.64 | 28.4 | 15.15 | 16.74 | 264193 | 243318 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DT | SA198DT | sa19 8dt | sa198dt | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 1064 | 1524 | Over1500 | 3.05 | 2.23 | 1.64 | 28.4 | 15.15 | 16.74 | 263751 | 243230 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DU | SA198DU | sa19 8du | sa198du | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 1926 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 263710 | 242342 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DX | SA198DX | sa19 8dx | sa198dx | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 2481 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 263370 | 240548 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8DY | SA198DY | sa19 8dy | sa198dy | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 2256 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 263358 | 241996 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8EA | SA198EA | sa19 8ea | sa198ea | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 976 | 1547 | Over1500 | 3.1 | 2.27 | 1.66 | 28.83 | 15.38 | 17 | 263038 | 243365 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8EB | SA198EB | sa19 8eb | sa198eb | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 896 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 262571 | 244078 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8EG | SA198EG | sa19 8eg | sa198eg | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3732 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 271367 | 231567 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8EH | SA198EH | sa19 8eh | sa198eh | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3507 | 1348 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.12 | 13.4 | 14.81 | 271391 | 231309 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8EJ | SA198EJ | sa19 8ej | sa198ej | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 2479 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 262821 | 241853 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8EL | SA198EL | sa19 8el | sa198el | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3995 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 271723 | 231689 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8EN | SA198EN | sa19 8en | sa198en | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 3458 | 1395 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26 | 13.87 | 15.33 | 272760 | 232408 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8EP | SA198EP | sa19 8ep | sa198ep | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 4233 | 1439 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.82 | 14.3 | 15.81 | 271932 | 232640 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8EQ | SA198EQ | sa19 8eq | sa198eq | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 2789 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 263141 | 241213 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8ER | SA198ER | sa19 8er | sa198er | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 3675 | 1439 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.82 | 14.3 | 15.81 | 272459 | 233323 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8EW | SA198EW | sa19 8ew | sa198ew | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 3658 | 1418 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.43 | 14.1 | 15.58 | 272532 | 232523 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8EX | SA198EX | sa19 8ex | sa198ex | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1471 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 266111 | 245216 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HD | SA198HD | sa19 8hd | sa198hd | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3580 | 1348 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.12 | 13.4 | 14.81 | 271253 | 231450 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HE | SA198HE | sa19 8he | sa198he | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3051 | 1348 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.12 | 13.4 | 14.81 | 270945 | 231002 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HF | SA198HF | sa19 8hf | sa198hf | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2941 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 270073 | 231075 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HG | SA198HG | sa19 8hg | sa198hg | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3119 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 269828 | 231258 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HH | SA198HH | sa19 8hh | sa198hh | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3332 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 269589 | 231458 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HJ | SA198HJ | sa19 8hj | sa198hj | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 2732 | 1550 | Over1500 | 3.1 | 2.27 | 1.66 | 28.89 | 15.41 | 17.03 | 267365 | 245490 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HL | SA198HL | sa19 8hl | sa198hl | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3470 | 1422 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.5 | 14.14 | 15.62 | 269520 | 231590 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HN | SA198HN | sa19 8hn | sa198hn | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 4321 | 1422 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.5 | 14.14 | 15.62 | 269844 | 232460 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HQ | SA198HQ | sa19 8hq | sa198hq | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1671 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 266404 | 245019 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HR | SA198HR | sa19 8hr | sa198hr | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 3986 | 1465 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.31 | 14.56 | 16.1 | 267995 | 232348 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HS | SA198HS | sa19 8hs | sa198hs | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 4939 | 1517 | Over1500 | 3.04 | 2.22 | 1.63 | 28.27 | 15.08 | 16.67 | 268814 | 233081 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HU | SA198HU | sa19 8hu | sa198hu | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 4499 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 268391 | 232962 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HW | SA198HW | sa19 8hw | sa198hw | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 4192 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 269352 | 232297 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HY | SA198HY | sa19 8hy | sa198hy | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 4104 | 1422 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.5 | 14.14 | 15.62 | 270224 | 232230 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8HZ | SA198HZ | sa19 8hz | sa198hz | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 4577 | 1603 | Over1500 | 3.21 | 2.35 | 1.72 | 29.88 | 15.93 | 17.61 | 269203 | 245796 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JA | SA198JA | sa19 8ja | sa198ja | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 5262 | 1644 | Over1500 | 3.29 | 2.41 | 1.77 | 30.64 | 16.34 | 18.06 | 269688 | 246497 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JB | SA198JB | sa19 8jb | sa198jb | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 4220 | 1578 | Over1500 | 3.16 | 2.31 | 1.69 | 29.41 | 15.69 | 17.34 | 268957 | 245271 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JD | SA198JD | sa19 8jd | sa198jd | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 3415 | 1558 | Over1500 | 3.12 | 2.28 | 1.67 | 29.04 | 15.49 | 17.12 | 268214 | 244519 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JE | SA198JE | sa19 8je | sa198je | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 362 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 265058 | 244804 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JF | SA198JF | sa19 8jf | sa198jf | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 470 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 265149 | 244865 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JG | SA198JG | sa19 8jg | sa198jg | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1535 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 265969 | 245545 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JH | SA198JH | sa19 8jh | sa198jh | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 2707 | 1584 | Over1500 | 3.17 | 2.32 | 1.7 | 29.52 | 15.75 | 17.4 | 266854 | 246313 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JJ | SA198JJ | sa19 8jj | sa198jj | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 3461 | 1583 | Over1500 | 3.17 | 2.32 | 1.7 | 29.5 | 15.74 | 17.39 | 267260 | 246984 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JL | SA198JL | sa19 8jl | sa198jl | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 159 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 264940 | 244625 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JN | SA198JN | sa19 8jn | sa198jn | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 194 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 264993 | 244533 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JP | SA198JP | sa19 8jp | sa198jp | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 642 | 1517 | Over1500 | 3.04 | 2.22 | 1.63 | 28.27 | 15.08 | 16.67 | 264982 | 243934 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JQ | SA198JQ | sa19 8jq | sa198jq | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 2064 | 1550 | Over1500 | 3.1 | 2.27 | 1.66 | 28.89 | 15.41 | 17.03 | 266649 | 245466 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JR | SA198JR | sa19 8jr | sa198jr | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1738 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 264520 | 246265 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JT | SA198JT | sa19 8jt | sa198jt | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1955 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 264520 | 246485 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JU | SA198JU | sa19 8ju | sa198ju | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 2434 | 1534 | Over1500 | 3.07 | 2.25 | 1.65 | 28.59 | 15.25 | 16.85 | 264083 | 246876 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JW | SA198JW | sa19 8jw | sa198jw | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 774 | 1550 | Over1500 | 3.1 | 2.27 | 1.66 | 28.89 | 15.41 | 17.03 | 265543 | 244334 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JX | SA198JX | sa19 8jx | sa198jx | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1944 | 1543 | Over1500 | 3.09 | 2.26 | 1.66 | 28.76 | 15.34 | 16.95 | 264023 | 246332 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JY | SA198JY | sa19 8jy | sa198jy | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 1475 | 1543 | Over1500 | 3.09 | 2.26 | 1.66 | 28.76 | 15.34 | 16.95 | 263601 | 245717 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8JZ | SA198JZ | sa19 8jz | sa198jz | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1013 | 1499 | 1200to1500 | 3 | 2.2 | 1.61 | 27.94 | 14.9 | 16.47 | 264217 | 245378 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LE | SA198LE | sa19 8le | sa198le | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3372 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 269397 | 231475 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LF | SA198LF | sa19 8lf | sa198lf | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3335 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 269396 | 231438 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LG | SA198LG | sa19 8lg | sa198lg | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3163 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 269439 | 231270 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LH | SA198LH | sa19 8lh | sa198lh | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2647 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 269435 | 230747 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LJ | SA198LJ | sa19 8lj | sa198lj | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 296 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 264970 | 244792 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LL | SA198LL | sa19 8ll | sa198ll | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2941 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 268913 | 230913 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LN | SA198LN | sa19 8ln | sa198ln | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2270 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 269471 | 230371 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LP | SA198LP | sa19 8lp | sa198lp | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3362 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 268213 | 231053 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LQ | SA198LQ | sa19 8lq | sa198lq | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 218 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 264943 | 244715 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LR | SA198LR | sa19 8lr | sa198lr | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3448 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 267993 | 231019 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LS | SA198LS | sa19 8ls | sa198ls | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 3699 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 267727 | 231386 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LT | SA198LT | sa19 8lt | sa198lt | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 3031 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 267078 | 231907 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LU | SA198LU | sa19 8lu | sa198lu | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 2650 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 266699 | 231753 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LW | SA198LW | sa19 8lw | sa198lw | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2463 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 268835 | 230365 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LX | SA198LX | sa19 8lx | sa198lx | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 868 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 264500 | 245364 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LY | SA198LY | sa19 8ly | sa198ly | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 3489 | 1465 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.31 | 14.56 | 16.1 | 267538 | 231799 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8LZ | SA198LZ | sa19 8lz | sa198lz | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1164 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 264753 | 245713 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NA | SA198NA | sa19 8na | sa198na | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 4064 | 1465 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.31 | 14.56 | 16.1 | 268170 | 231821 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NB | SA198NB | sa19 8nb | sa198nb | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3699 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 268831 | 231683 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8ND | SA198ND | sa19 8nd | sa198nd | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3353 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 269350 | 231449 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NH | SA198NH | sa19 8nh | sa198nh | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3943 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 269349 | 232045 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NL | SA198NL | sa19 8nl | sa198nl | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 4174 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 268889 | 232191 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NN | SA198NN | sa19 8nn | sa198nn | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 4444 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 268410 | 232637 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NP | SA198NP | sa19 8np | sa198np | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 3670 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 267542 | 232908 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NQ | SA198NQ | sa19 8nq | sa198nq | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 1508 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 264980 | 246047 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NR | SA198NR | sa19 8nr | sa198nr | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 3679 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 267513 | 234491 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NS | SA198NS | sa19 8ns | sa198ns | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 3269 | 1488 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.73 | 14.79 | 16.35 | 267114 | 234734 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NT | SA198NT | sa19 8nt | sa198nt | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 4691 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 268368 | 233613 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NW | SA198NW | sa19 8nw | sa198nw | Carmarthenshire | Sir Gaerfyrddin | Talley WwTW | 4040 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 267970 | 232757 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NX | SA198NX | sa19 8nx | sa198nx | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 2314 | 1563 | Over1500 | 3.13 | 2.29 | 1.68 | 29.13 | 15.54 | 17.17 | 265144 | 246838 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NY | SA198NY | sa19 8ny | sa198ny | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 4506 | 1613 | Over1500 | 3.23 | 2.36 | 1.73 | 30.06 | 16.03 | 17.72 | 271221 | 237061 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8NZ | SA198NZ | sa19 8nz | sa198nz | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 2495 | 1563 | Over1500 | 3.13 | 2.29 | 1.68 | 29.13 | 15.54 | 17.17 | 264947 | 247040 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PA | SA198PA | sa19 8pa | sa198pa | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 4891 | 1613 | Over1500 | 3.23 | 2.36 | 1.73 | 30.06 | 16.03 | 17.72 | 271451 | 236719 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PB | SA198PB | sa19 8pb | sa198pb | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 5232 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 271289 | 235994 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PD | SA198PD | sa19 8pd | sa198pd | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 4830 | 1505 | Over1500 | 3.01 | 2.2 | 1.62 | 28.05 | 14.96 | 16.54 | 271950 | 235598 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PE | SA198PE | sa19 8pe | sa198pe | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 4853 | 1505 | Over1500 | 3.01 | 2.2 | 1.62 | 28.05 | 14.96 | 16.54 | 272190 | 236035 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PF | SA198PF | sa19 8pf | sa198pf | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 333 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 267672 | 239885 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PG | SA198PG | sa19 8pg | sa198pg | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 1176 | 1576 | Over1500 | 3.15 | 2.31 | 1.69 | 29.37 | 15.67 | 17.32 | 268654 | 239827 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PH | SA198PH | sa19 8ph | sa198ph | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 1103 | 1551 | Over1500 | 3.1 | 2.27 | 1.67 | 28.91 | 15.42 | 17.04 | 268487 | 239108 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PJ | SA198PJ | sa19 8pj | sa198pj | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 5084 | 1629 | Over1500 | 3.26 | 2.39 | 1.75 | 30.36 | 16.19 | 17.9 | 267499 | 248857 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PL | SA198PL | sa19 8pl | sa198pl | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 1524 | 1579 | Over1500 | 3.16 | 2.31 | 1.7 | 29.43 | 15.7 | 17.35 | 268996 | 239309 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PN | SA198PN | sa19 8pn | sa198pn | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 1746 | 1579 | Over1500 | 3.16 | 2.31 | 1.7 | 29.43 | 15.7 | 17.35 | 269034 | 238767 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PP | SA198PP | sa19 8pp | sa198pp | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 2545 | 1619 | Over1500 | 3.24 | 2.37 | 1.74 | 30.18 | 16.09 | 17.79 | 270018 | 239237 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PQ | SA198PQ | sa19 8pq | sa198pq | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 3634 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 265933 | 248002 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PR | SA198PR | sa19 8pr | sa198pr | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 3584 | 1630 | Over1500 | 3.26 | 2.39 | 1.75 | 30.38 | 16.2 | 17.91 | 271047 | 240106 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PS | SA198PS | sa19 8ps | sa198ps | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 2678 | 1617 | Over1500 | 3.24 | 2.37 | 1.74 | 30.14 | 16.07 | 17.77 | 270157 | 239930 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PU | SA198PU | sa19 8pu | sa198pu | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1379 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 266690 | 238438 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PW | SA198PW | sa19 8pw | sa198pw | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 2200 | 1619 | Over1500 | 3.24 | 2.37 | 1.74 | 30.18 | 16.09 | 17.79 | 269611 | 238981 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PX | SA198PX | sa19 8px | sa198px | Carmarthenshire | Sir Gaerfyrddin | Llanfair Clydogau WwTW | 5483 | 1641 | Over1500 | 3.28 | 2.4 | 1.76 | 30.59 | 16.31 | 18.03 | 267450 | 249654 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PY | SA198PY | sa19 8py | sa198py | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 932 | 1503 | Over1500 | 3.01 | 2.2 | 1.61 | 28.01 | 14.94 | 16.51 | 267099 | 238759 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8PZ | SA198PZ | sa19 8pz | sa198pz | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 165 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 264818 | 244714 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QA | SA198QA | sa19 8qa | sa198qa | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 691 | 1499 | 1200to1500 | 3 | 2.2 | 1.61 | 27.94 | 14.9 | 16.47 | 264019 | 244642 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QB | SA198QB | sa19 8qb | sa198qb | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 414 | 1499 | 1200to1500 | 3 | 2.2 | 1.61 | 27.94 | 14.9 | 16.47 | 263727 | 244558 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QD | SA198QD | sa19 8qd | sa198qd | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 406 | 1513 | Over1500 | 3.03 | 2.22 | 1.62 | 28.2 | 15.04 | 16.62 | 263847 | 244165 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QE | SA198QE | sa19 8qe | sa198qe | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 381 | 1499 | 1200to1500 | 3 | 2.2 | 1.61 | 27.94 | 14.9 | 16.47 | 263605 | 244598 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QF | SA198QF | sa19 8qf | sa198qf | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 617 | 1517 | Over1500 | 3.04 | 2.22 | 1.63 | 28.27 | 15.08 | 16.67 | 263043 | 244713 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QG | SA198QG | sa19 8qg | sa198qg | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 264 | 1508 | Over1500 | 3.02 | 2.21 | 1.62 | 28.11 | 14.99 | 16.57 | 263212 | 244365 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QH | SA198QH | sa19 8qh | sa198qh | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 1605 | 1468 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.36 | 14.59 | 16.13 | 261956 | 244836 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QJ | SA198QJ | sa19 8qj | sa198qj | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 2213 | 1482 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.62 | 14.73 | 16.28 | 261699 | 245603 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QL | SA198QL | sa19 8ql | sa198ql | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 2289 | 1482 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.62 | 14.73 | 16.28 | 262379 | 246272 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QN | SA198QN | sa19 8qn | sa198qn | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 1555 | 1503 | Over1500 | 3.01 | 2.2 | 1.61 | 28.01 | 14.94 | 16.51 | 262842 | 245681 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QP | SA198QP | sa19 8qp | sa198qp | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 969 | 1517 | Over1500 | 3.04 | 2.22 | 1.63 | 28.27 | 15.08 | 16.67 | 263243 | 245196 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QQ | SA198QQ | sa19 8qq | sa198qq | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 986 | 1517 | Over1500 | 3.04 | 2.22 | 1.63 | 28.27 | 15.08 | 16.67 | 262631 | 244798 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QR | SA198QR | sa19 8qr | sa198qr | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 372 | 1499 | 1200to1500 | 3 | 2.2 | 1.61 | 27.94 | 14.9 | 16.47 | 263700 | 244526 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8QS | SA198QS | sa19 8qs | sa198qs | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 385 | 1499 | 1200to1500 | 3 | 2.2 | 1.61 | 27.94 | 14.9 | 16.47 | 263626 | 244592 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RA | SA198RA | sa19 8ra | sa198ra | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 233 | 1503 | Over1500 | 3.01 | 2.2 | 1.61 | 28.01 | 14.94 | 16.51 | 267490 | 239367 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RB | SA198RB | sa19 8rb | sa198rb | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 444 | 1503 | Over1500 | 3.01 | 2.2 | 1.61 | 28.01 | 14.94 | 16.51 | 267229 | 239249 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RD | SA198RD | sa19 8rd | sa198rd | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 241 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 267496 | 239841 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RE | SA198RE | sa19 8re | sa198re | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 344 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 267560 | 239939 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RF | SA198RF | sa19 8rf | sa198rf | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 436 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 267622 | 240018 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RG | SA198RG | sa19 8rg | sa198rg | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 706 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 267964 | 240132 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RH | SA198RH | sa19 8rh | sa198rh | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 377 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 267128 | 239542 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RL | SA198RL | sa19 8rl | sa198rl | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 416 | 1503 | Over1500 | 3.01 | 2.2 | 1.61 | 28.01 | 14.94 | 16.51 | 267143 | 239387 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RN | SA198RN | sa19 8rn | sa198rn | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 772 | 1503 | Over1500 | 3.01 | 2.2 | 1.61 | 28.01 | 14.94 | 16.51 | 266975 | 239034 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RP | SA198RP | sa19 8rp | sa198rp | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 1167 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 266364 | 239333 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RR | SA198RR | sa19 8rr | sa198rr | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 737 | 1483 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.64 | 14.74 | 16.29 | 266294 | 239969 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RS | SA198RS | sa19 8rs | sa198rs | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 555 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 267197 | 240065 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RW | SA198RW | sa19 8rw | sa198rw | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 1067 | 1503 | Over1500 | 3.01 | 2.2 | 1.61 | 28.01 | 14.94 | 16.51 | 266527 | 239163 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8RY | SA198RY | sa19 8ry | sa198ry | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 174 | 1500 |  | 3 | 2.2 | 1.61 | 27.96 | 14.91 | 16.48 | 265746 | 237672 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SA | SA198SA | sa19 8sa | sa198sa | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 786 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 264885 | 237254 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SB | SA198SB | sa19 8sb | sa198sb | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 903 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 264677 | 237635 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SD | SA198SD | sa19 8sd | sa198sd | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 919 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 264756 | 237214 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SE | SA198SE | sa19 8se | sa198se | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1556 | 1506 | Over1500 | 3.01 | 2.21 | 1.62 | 28.07 | 14.97 | 16.55 | 264567 | 236439 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SF | SA198SF | sa19 8sf | sa198sf | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1483 | 1506 | Over1500 | 3.01 | 2.21 | 1.62 | 28.07 | 14.97 | 16.55 | 264696 | 236430 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SG | SA198SG | sa19 8sg | sa198sg | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 2288 | 1506 | Over1500 | 3.01 | 2.21 | 1.62 | 28.07 | 14.97 | 16.55 | 264593 | 235506 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SH | SA198SH | sa19 8sh | sa198sh | Carmarthenshire | Sir Gaerfyrddin | Llansawel WwTW | 2023 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 264085 | 235029 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SL | SA198SL | sa19 8sl | sa198sl | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1219 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 264903 | 236606 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SN | SA198SN | sa19 8sn | sa198sn | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 985 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 265147 | 236735 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SR | SA198SR | sa19 8sr | sa198sr | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 811 | 1500 |  | 3 | 2.2 | 1.61 | 27.96 | 14.91 | 16.48 | 266113 | 238231 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SS | SA198SS | sa19 8ss | sa198ss | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1103 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 266140 | 238570 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8ST | SA198ST | sa19 8st | sa198st | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1036 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 265752 | 238641 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SU | SA198SU | sa19 8su | sa198su | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 1468 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 266102 | 239112 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SW | SA198SW | sa19 8sw | sa198sw | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 707 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 265341 | 236955 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8SY | SA198SY | sa19 8sy | sa198sy | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 1447 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 265596 | 239134 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TA | SA198TA | sa19 8ta | sa198ta | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 1299 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 265807 | 239260 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TB | SA198TB | sa19 8tb | sa198tb | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1492 | 1484 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.66 | 14.75 | 16.3 | 265437 | 239105 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TD | SA198TD | sa19 8td | sa198td | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 1314 | 1484 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.66 | 14.75 | 16.3 | 265160 | 239441 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TE | SA198TE | sa19 8te | sa198te | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1419 | 1484 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.66 | 14.75 | 16.3 | 264837 | 238829 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TF | SA198TF | sa19 8tf | sa198tf | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1407 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 264354 | 238310 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TG | SA198TG | sa19 8tg | sa198tg | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 984 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 264668 | 237988 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TH | SA198TH | sa19 8th | sa198th | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 391 | 1500 |  | 3 | 2.2 | 1.61 | 27.96 | 14.91 | 16.48 | 265817 | 237931 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TJ | SA198TJ | sa19 8tj | sa198tj | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 251 | 1500 |  | 3 | 2.2 | 1.61 | 27.96 | 14.91 | 16.48 | 265819 | 237695 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TN | SA198TN | sa19 8tn | sa198tn | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 502 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 266049 | 237441 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TP | SA198TP | sa19 8tp | sa198tp | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1494 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 266901 | 236922 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TR | SA198TR | sa19 8tr | sa198tr | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1882 | 1534 | Over1500 | 3.07 | 2.25 | 1.65 | 28.59 | 15.25 | 16.85 | 266850 | 236232 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TS | SA198TS | sa19 8ts | sa198ts | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1819 | 1541 | Over1500 | 3.08 | 2.26 | 1.66 | 28.72 | 15.32 | 16.93 | 266372 | 235983 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TU | SA198TU | sa19 8tu | sa198tu | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 2545 | 1486 | 1200to1500 | 2.97 | 2.18 | 1.6 | 27.7 | 14.77 | 16.33 | 266039 | 235117 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TW | SA198TW | sa19 8tw | sa198tw | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 590 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 266070 | 237291 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8TY | SA198TY | sa19 8ty | sa198ty | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 2889 | 1486 | 1200to1500 | 2.97 | 2.18 | 1.6 | 27.7 | 14.77 | 16.33 | 265589 | 234732 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UA | SA198UA | sa19 8ua | sa198ua | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 2426 | 1486 | 1200to1500 | 2.97 | 2.18 | 1.6 | 27.7 | 14.77 | 16.33 | 265560 | 235195 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UB | SA198UB | sa19 8ub | sa198ub | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 2114 | 1541 | Over1500 | 3.08 | 2.26 | 1.66 | 28.72 | 15.32 | 16.93 | 265522 | 235507 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UD | SA198UD | sa19 8ud | sa198ud | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1108 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 265786 | 236532 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UE | SA198UE | sa19 8ue | sa198ue | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1083 | 1500 |  | 3 | 2.2 | 1.61 | 27.96 | 14.91 | 16.48 | 266250 | 238470 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UG | SA198UG | sa19 8ug | sa198ug | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 901 | 1503 | Over1500 | 3.01 | 2.2 | 1.61 | 28.01 | 14.94 | 16.51 | 267267 | 238730 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UH | SA198UH | sa19 8uh | sa198uh | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1145 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 266692 | 237891 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UL | SA198UL | sa19 8ul | sa198ul | Carmarthenshire | Sir Gaerfyrddin | Crugybar STW | 1661 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 267209 | 237942 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UN | SA198UN | sa19 8un | sa198un | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 2205 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 268249 | 237527 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UP | SA198UP | sa19 8up | sa198up | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 758 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 266490 | 240966 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UR | SA198UR | sa19 8ur | sa198ur | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 504 | 1483 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.64 | 14.74 | 16.29 | 265954 | 240065 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8US | SA198US | sa19 8us | sa198us | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 494 | 1483 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.64 | 14.74 | 16.29 | 266313 | 240383 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UT | SA198UT | sa19 8ut | sa198ut | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 1660 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 267152 | 241589 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UU | SA198UU | sa19 8uu | sa198uu | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 2844 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 268047 | 242390 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UW | SA198UW | sa19 8uw | sa198uw | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 200 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 265653 | 240532 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8UY | SA198UY | sa19 8uy | sa198uy | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 2961 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 268377 | 242428 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YA | SA198YA | sa19 8ya | sa198ya | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 3870 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 268534 | 243537 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YB | SA198YB | sa19 8yb | sa198yb | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 4320 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 269116 | 244378 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YD | SA198YD | sa19 8yd | sa198yd | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 4708 | 1677 | Over1500 | 3.36 | 2.46 | 1.8 | 31.26 | 16.67 | 18.42 | 269504 | 244385 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YE | SA198YE | sa19 8ye | sa198ye | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 6175 | 1692 | Over1500 | 3.39 | 2.48 | 1.82 | 31.54 | 16.82 | 18.59 | 270914 | 245407 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YG | SA198YG | sa19 8yg | sa198yg | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 4633 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 269379 | 243850 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YH | SA198YH | sa19 8yh | sa198yh | Carmarthenshire | Sir Gaerfyrddin | Caio STW | 5297 | 1677 | Over1500 | 3.36 | 2.46 | 1.8 | 31.26 | 16.67 | 18.42 | 270127 | 244199 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YL | SA198YL | sa19 8yl | sa198yl | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 1102 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 266428 | 241497 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YN | SA198YN | sa19 8yn | sa198yn | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 2715 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 267033 | 243006 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YP | SA198YP | sa19 8yp | sa198yp | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 2760 | 1522 | Over1500 | 3.05 | 2.23 | 1.63 | 28.37 | 15.13 | 16.72 | 267355 | 243508 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YR | SA198YR | sa19 8yr | sa198yr | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 2872 | 1551 | Over1500 | 3.1 | 2.27 | 1.67 | 28.91 | 15.42 | 17.04 | 267634 | 244088 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YT | SA198YT | sa19 8yt | sa198yt | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 305 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 265584 | 240705 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YU | SA198YU | sa19 8yu | sa198yu | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 1156 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 265047 | 241388 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YW | SA198YW | sa19 8yw | sa198yw | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 2296 | 1522 | Over1500 | 3.05 | 2.23 | 1.63 | 28.37 | 15.13 | 16.72 | 266873 | 243565 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 8YY | SA198YY | sa19 8yy | sa198yy | Carmarthenshire | Sir Gaerfyrddin | Pumpsaint STW | 1814 | 1518 | Over1500 | 3.04 | 2.22 | 1.63 | 28.29 | 15.09 | 16.68 | 264939 | 242126 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AA | SA199AA | sa19 9aa | sa199aa | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 760 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270606 | 228395 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AB | SA199AB | sa19 9ab | sa199ab | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 862 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270723 | 228362 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AD | SA199AD | sa19 9ad | sa199ad | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 754 | 1284 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.93 | 12.76 | 14.11 | 270552 | 228501 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AE | SA199AE | sa19 9ae | sa199ae | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 674 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270504 | 228418 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AF | SA199AF | sa19 9af | sa199af | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 703 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270566 | 228333 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AG | SA199AG | sa19 9ag | sa199ag | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 748 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270613 | 228330 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AH | SA199AH | sa19 9ah | sa199ah | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 711 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270589 | 228267 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AJ | SA199AJ | sa19 9aj | sa199aj | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 3069 | 1502 | Over1500 | 3.01 | 2.2 | 1.61 | 27.99 | 14.93 | 16.5 | 277000 | 226741 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9AL | SA199AL | sa19 9al | sa199al | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 758 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270631 | 228301 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AN | SA199AN | sa19 9an | sa199an | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1800 | 1290 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.04 | 12.82 | 14.17 | 271513 | 228917 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AP | SA199AP | sa19 9ap | sa199ap | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2497 | 1272 | 1200to1500 | 2.55 | 1.86 | 1.37 | 23.71 | 12.64 | 13.98 | 271871 | 229659 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AQ | SA199AQ | sa19 9aq | sa199aq | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 2693 | 1502 | Over1500 | 3.01 | 2.2 | 1.61 | 27.99 | 14.93 | 16.5 | 277383 | 227074 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9AR | SA199AR | sa19 9ar | sa199ar | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3721 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 272553 | 230738 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AS | SA199AS | sa19 9as | sa199as | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3473 | 1246 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.22 | 12.39 | 13.69 | 272912 | 229850 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AT | SA199AT | sa19 9at | sa199at | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 3747 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 273159 | 230898 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AU | SA199AU | sa19 9au | sa199au | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3935 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 272584 | 231007 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9AW | SA199AW | sa19 9aw | sa199aw | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2454 | 1290 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.04 | 12.82 | 14.17 | 272093 | 229221 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9BB | SA199BB | sa19 9bb | sa199bb | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2710 | 1272 | 1200to1500 | 2.55 | 1.86 | 1.37 | 23.71 | 12.64 | 13.98 | 271773 | 230088 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9BD | SA199BD | sa19 9bd | sa199bd | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2024 | 1305 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.32 | 12.97 | 14.34 | 271161 | 229715 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9BE | SA199BE | sa19 9be | sa199be | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1560 | 1305 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.32 | 12.97 | 14.34 | 270580 | 229539 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9BG | SA199BG | sa19 9bg | sa199bg | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1432 | 1284 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.93 | 12.76 | 14.11 | 270843 | 229208 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9BR | SA199BR | sa19 9br | sa199br | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 770 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270659 | 228177 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9BS | SA199BS | sa19 9bs | sa199bs | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1207 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 270838 | 227393 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9BT | SA199BT | sa19 9bt | sa199bt | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1437 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 270872 | 227091 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9BU | SA199BU | sa19 9bu | sa199bu | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 762 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 270369 | 227548 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9BW | SA199BW | sa19 9bw | sa199bw | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 771 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270644 | 228298 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9BX | SA199BX | sa19 9bx | sa199bx | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 791 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270667 | 228289 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9BY | SA199BY | sa19 9by | sa199by | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 517 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 270284 | 227806 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9DA | SA199DA | sa19 9da | sa199da | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 351 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 269943 | 227793 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9DB | SA199DB | sa19 9db | sa199db | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 578 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 269931 | 227564 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9DD | SA199DD | sa19 9dd | sa199dd | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1504 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 269562 | 226673 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9DE | SA199DE | sa19 9de | sa199de | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1156 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 270618 | 227242 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9DG | SA199DG | sa19 9dg | sa199dg | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1772 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 269809 | 226370 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9DN | SA199DN | sa19 9dn | sa199dn | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 1760 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 269917 | 225505 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9DP | SA199DP | sa19 9dp | sa199dp | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 2295 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 270479 | 225274 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9DR | SA199DR | sa19 9dr | sa199dr | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 1980 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 270114 | 224743 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9DS | SA199DS | sa19 9ds | sa199ds | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 1805 | 1578 | Over1500 | 3.16 | 2.31 | 1.69 | 29.41 | 15.69 | 17.34 | 269519 | 223973 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9DT | SA199DT | sa19 9dt | sa199dt | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 1590 | 1524 | Over1500 | 3.05 | 2.23 | 1.64 | 28.4 | 15.15 | 16.74 | 268556 | 223644 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9DU | SA199DU | sa19 9du | sa199du | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2124 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 270440 | 226089 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9DW | SA199DW | sa19 9dw | sa199dw | Carmarthenshire | Sir Gaerfyrddin | Bethlehem STW | 2112 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 270253 | 225621 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9DY | SA199DY | sa19 9dy | sa199dy | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1979 | 1413 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.34 | 14.05 | 15.52 | 270842 | 226406 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9ED | SA199ED | sa19 9ed | sa199ed | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 917 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270804 | 228217 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9EE | SA199EE | sa19 9ee | sa199ee | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 795 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270666 | 228310 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9EF | SA199EF | sa19 9ef | sa199ef | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 849 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270725 | 228291 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9EG | SA199EG | sa19 9eg | sa199eg | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 820 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270695 | 228293 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9EH | SA199EH | sa19 9eh | sa199eh | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1086 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270974 | 228194 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9EL | SA199EL | sa19 9el | sa199el | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1818 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 271708 | 228136 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9EN | SA199EN | sa19 9en | sa199en | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1855 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 271739 | 228279 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9EP | SA199EP | sa19 9ep | sa199ep | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3490 | 1292 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.08 | 12.84 | 14.2 | 273324 | 227520 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9ER | SA199ER | sa19 9er | sa199er | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 3802 | 1317 | 1200to1500 | 2.64 | 1.93 | 1.41 | 24.55 | 13.09 | 14.47 | 273817 | 227575 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9ES | SA199ES | sa19 9es | sa199es | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 3156 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 273942 | 226919 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9ET | SA199ET | sa19 9et | sa199et | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 3284 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 274462 | 227262 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9EU | SA199EU | sa19 9eu | sa199eu | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 3442 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 274825 | 227641 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9EW | SA199EW | sa19 9ew | sa199ew | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2967 | 1292 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.08 | 12.84 | 14.2 | 272849 | 227927 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9EY | SA199EY | sa19 9ey | sa199ey | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 3073 | 1470 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.4 | 14.61 | 16.15 | 275503 | 227458 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9HA | SA199HA | sa19 9ha | sa199ha | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 3180 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 273352 | 226558 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9HB | SA199HB | sa19 9hb | sa199hb | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 3341 | 1478 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.55 | 14.69 | 16.24 | 272805 | 226237 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9HD | SA199HD | sa19 9hd | sa199hd | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2417 | 1506 | Over1500 | 3.01 | 2.21 | 1.62 | 28.07 | 14.97 | 16.55 | 272967 | 224244 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9HE | SA199HE | sa19 9he | sa199he | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3017 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 272509 | 226643 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9HF | SA199HF | sa19 9hf | sa199hf | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2095 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 271757 | 227191 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9HG | SA199HG | sa19 9hg | sa199hg | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1685 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 271249 | 227145 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9HN | SA199HN | sa19 9hn | sa199hn | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1157 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 271012 | 228420 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9HP | SA199HP | sa19 9hp | sa199hp | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1154 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 271025 | 228350 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9HR | SA199HR | sa19 9hr | sa199hr | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1507 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 271361 | 228464 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9HS | SA199HS | sa19 9hs | sa199hs | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1667 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 271542 | 228360 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9HT | SA199HT | sa19 9ht | sa199ht | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1873 | 1318 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.57 | 13.1 | 14.48 | 271736 | 228455 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9HU | SA199HU | sa19 9hu | sa199hu | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2615 | 1290 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.04 | 12.82 | 14.17 | 272450 | 228672 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9HW | SA199HW | sa19 9hw | sa199hw | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 924 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270771 | 228417 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9HY | SA199HY | sa19 9hy | sa199hy | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3200 | 1252 | 1200to1500 | 2.51 | 1.83 | 1.34 | 23.34 | 12.45 | 13.76 | 273051 | 228637 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9LA | SA199LA | sa19 9la | sa199la | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 3718 | 1317 | 1200to1500 | 2.64 | 1.93 | 1.41 | 24.55 | 13.09 | 14.47 | 273607 | 228101 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9LD | SA199LD | sa19 9ld | sa199ld | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 3286 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 274350 | 228958 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9LE | SA199LE | sa19 9le | sa199le | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 3218 | 1264 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.56 | 12.56 | 13.89 | 274330 | 229477 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9LF | SA199LF | sa19 9lf | sa199lf | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 3021 | 1262 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.52 | 12.54 | 13.87 | 274522 | 229974 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9LG | SA199LG | sa19 9lg | sa199lg | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 2644 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 274998 | 230505 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9LH | SA199LH | sa19 9lh | sa199lh | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 3084 | 1262 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.52 | 12.54 | 13.87 | 274529 | 230449 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9LL | SA199LL | sa19 9ll | sa199ll | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 999 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 270875 | 228303 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9LN | SA199LN | sa19 9ln | sa199ln | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 416 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 269817 | 228549 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9LP | SA199LP | sa19 9lp | sa199lp | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 789 | 1284 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.93 | 12.76 | 14.11 | 270552 | 228569 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9LR | SA199LR | sa19 9lr | sa199lr | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1025 | 1284 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.93 | 12.76 | 14.11 | 270511 | 228955 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9LS | SA199LS | sa19 9ls | sa199ls | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 639 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 270224 | 228685 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9LU | SA199LU | sa19 9lu | sa199lu | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 488 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 269969 | 228621 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9NA | SA199NA | sa19 9na | sa199na | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 736 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 269352 | 228642 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9NB | SA199NB | sa19 9nb | sa199nb | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 724 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 269279 | 228529 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9ND | SA199ND | sa19 9nd | sa199nd | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 808 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 269252 | 228636 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9NE | SA199NE | sa19 9ne | sa199ne | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 997 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 269127 | 228781 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9NF | SA199NF | sa19 9nf | sa199nf | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1581 | 1304 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.3 | 12.96 | 14.33 | 268737 | 229221 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9NG | SA199NG | sa19 9ng | sa199ng | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1539 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 269249 | 229539 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9NH | SA199NH | sa19 9nh | sa199nh | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2124 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 269185 | 230143 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9NN | SA199NN | sa19 9nn | sa199nn | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2308 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 269835 | 230447 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9NS | SA199NS | sa19 9ns | sa199ns | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 530 | 1776 | Over1500 | 3.55 | 2.6 | 1.91 | 33.1 | 17.65 | 19.51 | 272848 | 221265 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9NT | SA199NT | sa19 9nt | sa199nt | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 456 | 1761 | Over1500 | 3.52 | 2.58 | 1.89 | 32.82 | 17.51 | 19.35 | 272358 | 221419 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9NU | SA199NU | sa19 9nu | sa199nu | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 820 | 1761 | Over1500 | 3.52 | 2.58 | 1.89 | 32.82 | 17.51 | 19.35 | 272190 | 221088 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9NY | SA199NY | sa19 9ny | sa199ny | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1576 | 1987 | Over1500 | 3.98 | 2.91 | 2.13 | 37.03 | 19.75 | 21.83 | 272127 | 220277 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9PA | SA199PA | sa19 9pa | sa199pa | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1732 | 1908 | Over1500 | 3.82 | 2.79 | 2.05 | 35.56 | 18.97 | 20.96 | 273007 | 220063 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9PB | SA199PB | sa19 9pb | sa199pb | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1635 | 1908 | Over1500 | 3.82 | 2.79 | 2.05 | 35.56 | 18.97 | 20.96 | 273283 | 220249 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9PD | SA199PD | sa19 9pd | sa199pd | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1245 | 1839 | Over1500 | 3.68 | 2.69 | 1.98 | 34.28 | 18.28 | 20.2 | 273730 | 221124 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9PE | SA199PE | sa19 9pe | sa199pe | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 2485 | 1932 | Over1500 | 3.87 | 2.83 | 2.07 | 36.01 | 19.21 | 21.23 | 275073 | 221168 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9PF | SA199PF | sa19 9pf | sa199pf | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2046 | 1793 | Over1500 | 3.59 | 2.63 | 1.93 | 33.42 | 17.82 | 19.7 | 275372 | 222064 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9PG | SA199PG | sa19 9pg | sa199pg | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1909 | 1793 | Over1500 | 3.59 | 2.63 | 1.93 | 33.42 | 17.82 | 19.7 | 274550 | 222029 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9PH | SA199PH | sa19 9ph | sa199ph | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1345 | 1722 | Over1500 | 3.45 | 2.52 | 1.85 | 32.1 | 17.12 | 18.92 | 274004 | 221728 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9PP | SA199PP | sa19 9pp | sa199pp | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 1831 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 271237 | 226901 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA19 9PR | SA199PR | sa19 9pr | sa199pr | Carmarthenshire | Sir Gaerfyrddin | Llangadog STW | 2701 | 1413 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.34 | 14.05 | 15.52 | 271372 | 225882 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9PS | SA199PS | sa19 9ps | sa199ps | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 2198 | 1549 | Over1500 | 3.1 | 2.27 | 1.66 | 28.87 | 15.4 | 17.02 | 271634 | 223703 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9PT | SA199PT | sa19 9pt | sa199pt | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2630 | 1506 | Over1500 | 3.01 | 2.21 | 1.62 | 28.07 | 14.97 | 16.55 | 272779 | 224498 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9PU | SA199PU | sa19 9pu | sa199pu | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1495 | 1624 | Over1500 | 3.25 | 2.38 | 1.74 | 30.27 | 16.14 | 17.84 | 272370 | 223226 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9PY | SA199PY | sa19 9py | sa199py | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 2134 | 1506 | Over1500 | 3.01 | 2.21 | 1.62 | 28.07 | 14.97 | 16.55 | 272571 | 223892 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RA | SA199RA | sa19 9ra | sa199ra | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1467 | 1584 | Over1500 | 3.17 | 2.32 | 1.7 | 29.52 | 15.75 | 17.4 | 273389 | 223033 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RB | SA199RB | sa19 9rb | sa199rb | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 122 | 1671 | Over1500 | 3.34 | 2.45 | 1.79 | 31.14 | 16.61 | 18.36 | 272572 | 221845 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RD | SA199RD | sa19 9rd | sa199rd | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 406 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 272368 | 222042 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RE | SA199RE | sa19 9re | sa199re | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 467 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 272255 | 221992 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RF | SA199RF | sa19 9rf | sa199rf | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1013 | 1656 | Over1500 | 3.31 | 2.43 | 1.78 | 30.87 | 16.46 | 18.19 | 271651 | 221668 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RG | SA199RG | sa19 9rg | sa199rg | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1239 | 1761 | Over1500 | 3.52 | 2.58 | 1.89 | 32.82 | 17.51 | 19.35 | 271590 | 221136 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RH | SA199RH | sa19 9rh | sa199rh | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 2109 | 1673 | Over1500 | 3.35 | 2.45 | 1.8 | 31.18 | 16.63 | 18.38 | 270558 | 221596 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RL | SA199RL | sa19 9rl | sa199rl | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 2605 | 1757 | Over1500 | 3.52 | 2.57 | 1.89 | 32.75 | 17.47 | 19.3 | 269889 | 221410 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RN | SA199RN | sa19 9rn | sa199rn | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1685 | 1655 | Over1500 | 3.31 | 2.42 | 1.78 | 30.85 | 16.45 | 18.18 | 271271 | 222714 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RP | SA199RP | sa19 9rp | sa199rp | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 2349 | 1738 | Over1500 | 3.48 | 2.55 | 1.87 | 32.39 | 17.28 | 19.1 | 270586 | 220658 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RR | SA199RR | sa19 9rr | sa199rr | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 2740 | 1889 | Over1500 | 3.78 | 2.77 | 2.03 | 35.21 | 18.78 | 20.75 | 270596 | 219959 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RS | SA199RS | sa19 9rs | sa199rs | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 2921 | 1844 | Over1500 | 3.69 | 2.7 | 1.98 | 34.37 | 18.33 | 20.26 | 270176 | 220224 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RT | SA199RT | sa19 9rt | sa199rt | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 3172 | 1734 | Over1500 | 3.47 | 2.54 | 1.86 | 32.32 | 17.24 | 19.05 | 269341 | 219525 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RU | SA199RU | sa19 9ru | sa199ru | Carmarthenshire | Sir Gaerfyrddin | Trapp STW | 2975 | 1764 | Over1500 | 3.53 | 2.58 | 1.89 | 32.88 | 17.54 | 19.38 | 268334 | 218908 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RW | SA199RW | sa19 9rw | sa199rw | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1974 | 1655 | Over1500 | 3.31 | 2.42 | 1.78 | 30.85 | 16.45 | 18.18 | 271036 | 222882 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9RY | SA199RY | sa19 9ry | sa199ry | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 1823 | 1686 | Over1500 | 3.37 | 2.47 | 1.81 | 31.42 | 16.76 | 18.52 | 268374 | 220487 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9SA | SA199SA | sa19 9sa | sa199sa | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 1594 | 1639 | Over1500 | 3.28 | 2.4 | 1.76 | 30.55 | 16.29 | 18.01 | 268933 | 221806 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9SB | SA199SB | sa19 9sb | sa199sb | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 2301 | 1702 | Over1500 | 3.41 | 2.49 | 1.83 | 31.72 | 16.92 | 18.7 | 269648 | 221872 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9SD | SA199SD | sa19 9sd | sa199sd | Carmarthenshire | Sir Gaerfyrddin | Bryngwyn WwTW | 2876 | 1757 | Over1500 | 3.52 | 2.57 | 1.89 | 32.75 | 17.47 | 19.3 | 269873 | 220614 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9SL | SA199SL | sa19 9sl | sa199sl | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1118 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 274269 | 223989 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9SN | SA199SN | sa19 9sn | sa199sn | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 620 | 1591 | Over1500 | 3.18 | 2.33 | 1.71 | 29.65 | 15.82 | 17.48 | 274760 | 224096 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9SP | SA199SP | sa19 9sp | sa199sp | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 297 | 1591 | Over1500 | 3.18 | 2.33 | 1.71 | 29.65 | 15.82 | 17.48 | 275249 | 224377 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9SR | SA199SR | sa19 9sr | sa199sr | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1220 | 1543 | Over1500 | 3.09 | 2.26 | 1.66 | 28.76 | 15.34 | 16.95 | 274677 | 225107 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9SS | SA199SS | sa19 9ss | sa199ss | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1875 | 1485 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.68 | 14.76 | 16.32 | 274696 | 225855 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9ST | SA199ST | sa19 9st | sa199st | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2121 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 273330 | 224651 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9SU | SA199SU | sa19 9su | sa199su | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2089 | 1506 | Over1500 | 3.01 | 2.21 | 1.62 | 28.07 | 14.97 | 16.55 | 273323 | 223747 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9SW | SA199SW | sa19 9sw | sa199sw | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 518 | 1591 | Over1500 | 3.18 | 2.33 | 1.71 | 29.65 | 15.82 | 17.48 | 274966 | 224421 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9SY | SA199SY | sa19 9sy | sa199sy | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1892 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 273585 | 223513 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TA | SA199TA | sa19 9ta | sa199ta | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1476 | 1631 | Over1500 | 3.26 | 2.39 | 1.75 | 30.4 | 16.21 | 17.92 | 273825 | 222666 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TB | SA199TB | sa19 9tb | sa199tb | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 1332 | 1631 | Over1500 | 3.26 | 2.39 | 1.75 | 30.4 | 16.21 | 17.92 | 273710 | 222579 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TD | SA199TD | sa19 9td | sa199td | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 799 | 1671 | Over1500 | 3.34 | 2.45 | 1.79 | 31.14 | 16.61 | 18.36 | 273416 | 222019 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TE | SA199TE | sa19 9te | sa199te | Carmarthenshire | Sir Gaerfyrddin | Gwynfe STW | 454 | 1671 | Over1500 | 3.34 | 2.45 | 1.79 | 31.14 | 16.61 | 18.36 | 273016 | 222042 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TF | SA199TF | sa19 9tf | sa199tf | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1851 | 1631 | Over1500 | 3.26 | 2.39 | 1.75 | 30.4 | 16.21 | 17.92 | 273698 | 223338 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TG | SA199TG | sa19 9tg | sa199tg | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1431 | 1631 | Over1500 | 3.26 | 2.39 | 1.75 | 30.4 | 16.21 | 17.92 | 274165 | 223354 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TH | SA199TH | sa19 9th | sa199th | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1899 | 1793 | Over1500 | 3.59 | 2.63 | 1.93 | 33.42 | 17.82 | 19.7 | 274539 | 222408 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TL | SA199TL | sa19 9tl | sa199tl | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1268 | 1676 | Over1500 | 3.35 | 2.45 | 1.8 | 31.24 | 16.66 | 18.41 | 275158 | 222862 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TN | SA199TN | sa19 9tn | sa199tn | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1629 | 1769 | Over1500 | 3.54 | 2.59 | 1.9 | 32.97 | 17.58 | 19.44 | 275707 | 222515 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TP | SA199TP | sa19 9tp | sa199tp | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1238 | 1769 | Over1500 | 3.54 | 2.59 | 1.9 | 32.97 | 17.58 | 19.44 | 276420 | 223438 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TR | SA199TR | sa19 9tr | sa199tr | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1029 | 1676 | Over1500 | 3.35 | 2.45 | 1.8 | 31.24 | 16.66 | 18.41 | 274705 | 223334 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TW | SA199TW | sa19 9tw | sa199tw | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1187 | 1769 | Over1500 | 3.54 | 2.59 | 1.9 | 32.97 | 17.58 | 19.44 | 275545 | 222935 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9TY | SA199TY | sa19 9ty | sa199ty | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 234 | 1591 | Over1500 | 3.18 | 2.33 | 1.71 | 29.65 | 15.82 | 17.48 | 275322 | 224337 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UA | SA199UA | sa19 9ua | sa199ua | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 586 | 1577 | Over1500 | 3.16 | 2.31 | 1.69 | 29.39 | 15.68 | 17.33 | 275942 | 224275 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UB | SA199UB | sa19 9ub | sa199ub | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 907 | 1549 | Over1500 | 3.1 | 2.27 | 1.66 | 28.87 | 15.4 | 17.02 | 276187 | 224524 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UD | SA199UD | sa19 9ud | sa199ud | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1061 | 1577 | Over1500 | 3.16 | 2.31 | 1.69 | 29.39 | 15.68 | 17.33 | 276397 | 224413 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UE | SA199UE | sa19 9ue | sa199ue | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1619 | 1602 | Over1500 | 3.21 | 2.35 | 1.72 | 29.86 | 15.92 | 17.6 | 276895 | 224680 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UF | SA199UF | sa19 9uf | sa199uf | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1577 | 1602 | Over1500 | 3.21 | 2.35 | 1.72 | 29.86 | 15.92 | 17.6 | 276790 | 224816 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UG | SA199UG | sa19 9ug | sa199ug | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2058 | 1602 | Over1500 | 3.21 | 2.35 | 1.72 | 29.86 | 15.92 | 17.6 | 277166 | 225131 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UH | SA199UH | sa19 9uh | sa199uh | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2370 | 1602 | Over1500 | 3.21 | 2.35 | 1.72 | 29.86 | 15.92 | 17.6 | 277490 | 225188 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UL | SA199UL | sa19 9ul | sa199ul | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2383 | 1646 | Over1500 | 3.29 | 2.41 | 1.77 | 30.68 | 16.36 | 18.08 | 277724 | 224534 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UN | SA199UN | sa19 9un | sa199un | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 4318 | 1953 | Over1500 | 3.91 | 2.86 | 2.1 | 36.4 | 19.41 | 21.46 | 279691 | 223889 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UP | SA199UP | sa19 9up | sa199up | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2358 | 1646 | Over1500 | 3.29 | 2.41 | 1.77 | 30.68 | 16.36 | 18.08 | 277640 | 224780 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UR | SA199UR | sa19 9ur | sa199ur | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1507 | 1633 | Over1500 | 3.27 | 2.39 | 1.75 | 30.44 | 16.23 | 17.94 | 276862 | 223840 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UW | SA199UW | sa19 9uw | sa199uw | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 3039 | 1752 | Over1500 | 3.51 | 2.57 | 1.88 | 32.65 | 17.42 | 19.25 | 278411 | 223895 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9UY | SA199UY | sa19 9uy | sa199uy | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 459 | 1543 | Over1500 | 3.09 | 2.26 | 1.66 | 28.76 | 15.34 | 16.95 | 275297 | 224561 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YA | SA199YA | sa19 9ya | sa199ya | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 390 | 1577 | Over1500 | 3.16 | 2.31 | 1.69 | 29.39 | 15.68 | 17.33 | 275503 | 224480 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YB | SA199YB | sa19 9yb | sa199yb | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1108 | 1549 | Over1500 | 3.1 | 2.27 | 1.66 | 28.87 | 15.4 | 17.02 | 275930 | 225072 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YD | SA199YD | sa19 9yd | sa199yd | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1728 | 1602 | Over1500 | 3.21 | 2.35 | 1.72 | 29.86 | 15.92 | 17.6 | 276624 | 225309 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YE | SA199YE | sa19 9ye | sa199ye | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1487 | 1549 | Over1500 | 3.1 | 2.27 | 1.66 | 28.87 | 15.4 | 17.02 | 276170 | 225369 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YF | SA199YF | sa19 9yf | sa199yf | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2245 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 277028 | 225634 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YG | SA199YG | sa19 9yg | sa199yg | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2603 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 277281 | 225888 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YH | SA199YH | sa19 9yh | sa199yh | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2176 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 276717 | 225826 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YL | SA199YL | sa19 9yl | sa199yl | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 2340 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 276511 | 226158 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YN | SA199YN | sa19 9yn | sa199yn | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 1951 | 1532 | Over1500 | 3.07 | 2.24 | 1.65 | 28.55 | 15.23 | 16.83 | 275549 | 226053 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YP | SA199YP | sa19 9yp | sa199yp | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 3963 | 1714 | Over1500 | 3.43 | 2.51 | 1.84 | 31.95 | 17.04 | 18.83 | 278873 | 226033 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YR | SA199YR | sa19 9yr | sa199yr | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 3244 | 1566 | Over1500 | 3.13 | 2.29 | 1.68 | 29.19 | 15.57 | 17.21 | 279122 | 226933 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YS | SA199YS | sa19 9ys | sa199ys | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 2643 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 278936 | 227521 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YT | SA199YT | sa19 9yt | sa199yt | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 2502 | 1519 | Over1500 | 3.04 | 2.22 | 1.63 | 28.31 | 15.1 | 16.69 | 278294 | 227378 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YU | SA199YU | sa19 9yu | sa199yu | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 2322 | 1519 | Over1500 | 3.04 | 2.22 | 1.63 | 28.31 | 15.1 | 16.69 | 277610 | 227442 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YW | SA199YW | sa19 9yw | sa199yw | Carmarthenshire | Sir Gaerfyrddin | Twynllanan STW | 3190 | 1627 | Over1500 | 3.26 | 2.38 | 1.75 | 30.32 | 16.17 | 17.88 | 277880 | 226090 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA19 9YY | SA199YY | sa19 9yy | sa199yy | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 2132 | 1450 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.03 | 14.41 | 15.93 | 277304 | 227643 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0AA | SA200AA | sa20 0aa | sa200aa | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1321 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276734 | 234355 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AB | SA200AB | sa20 0ab | sa200ab | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1346 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276736 | 234382 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AG | SA200AG | sa20 0ag | sa200ag | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 723 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276173 | 233902 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AJ | SA200AJ | sa20 0aj | sa200aj | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 5367 | 1573 | Over1500 | 3.15 | 2.3 | 1.69 | 29.32 | 15.64 | 17.28 | 284948 | 236933 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AL | SA200AL | sa20 0al | sa200al | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1722 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276722 | 234797 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AN | SA200AN | sa20 0an | sa200an | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1311 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276799 | 234307 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AP | SA200AP | sa20 0ap | sa200ap | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1260 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276688 | 234309 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AR | SA200AR | sa20 0ar | sa200ar | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1227 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276595 | 234315 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AS | SA200AS | sa20 0as | sa200as | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 781 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276241 | 233953 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AT | SA200AT | sa20 0at | sa200at | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1177 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276519 | 234291 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AU | SA200AU | sa20 0au | sa200au | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1095 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276461 | 234224 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AW | SA200AW | sa20 0aw | sa200aw | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1313 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276762 | 234331 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AX | SA200AX | sa20 0ax | sa200ax | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 5199 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 284005 | 236047 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AY | SA200AY | sa20 0ay | sa200ay | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 973 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276438 | 234103 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0AZ | SA200AZ | sa20 0az | sa200az | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 808 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276131 | 233988 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BA | SA200BA | sa20 0ba | sa200ba | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 959 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276292 | 234125 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BB | SA200BB | sa20 0bb | sa200bb | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1132 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276400 | 234279 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BD | SA200BD | sa20 0bd | sa200bd | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1256 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276389 | 234409 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BE | SA200BE | sa20 0be | sa200be | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1334 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276344 | 234496 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BG | SA200BG | sa20 0bg | sa200bg | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1366 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 276332 | 234531 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BH | SA200BH | sa20 0bh | sa200bh | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1270 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276463 | 234405 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BJ | SA200BJ | sa20 0bj | sa200bj | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 713 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276290 | 233875 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BL | SA200BL | sa20 0bl | sa200bl | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1191 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276484 | 234317 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BN | SA200BN | sa20 0bn | sa200bn | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1317 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276652 | 234389 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BP | SA200BP | sa20 0bp | sa200bp | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1182 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276323 | 234346 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BQ | SA200BQ | sa20 0bq | sa200bq | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1310 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276538 | 234425 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BR | SA200BR | sa20 0br | sa200br | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1259 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276340 | 234421 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BS | SA200BS | sa20 0bs | sa200bs | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1405 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276820 | 234404 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BT | SA200BT | sa20 0bt | sa200bt | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1424 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276834 | 234417 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BU | SA200BU | sa20 0bu | sa200bu | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1508 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276920 | 234464 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BW | SA200BW | sa20 0bw | sa200bw | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1121 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276361 | 234277 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BX | SA200BX | sa20 0bx | sa200bx | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1408 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276789 | 234424 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BY | SA200BY | sa20 0by | sa200by | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1586 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 277024 | 234490 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0BZ | SA200BZ | sa20 0bz | sa200bz | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1476 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276760 | 234514 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DA | SA200DA | sa20 0da | sa200da | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1644 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 277071 | 234528 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DB | SA200DB | sa20 0db | sa200db | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1570 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 277038 | 234460 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DD | SA200DD | sa20 0dd | sa200dd | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1510 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 277048 | 234379 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DE | SA200DE | sa20 0de | sa200de | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1593 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 277178 | 234379 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DF | SA200DF | sa20 0df | sa200df | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1724 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 277212 | 234522 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DG | SA200DG | sa20 0dg | sa200dg | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1501 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276967 | 234426 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DH | SA200DH | sa20 0dh | sa200dh | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1676 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 277029 | 234594 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DJ | SA200DJ | sa20 0dj | sa200dj | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 447 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276108 | 233626 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DL | SA200DL | sa20 0dl | sa200dl | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1802 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 277016 | 234749 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DN | SA200DN | sa20 0dn | sa200dn | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1760 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276961 | 234731 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DP | SA200DP | sa20 0dp | sa200dp | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1656 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276808 | 234690 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DQ | SA200DQ | sa20 0dq | sa200dq | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1594 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276713 | 234663 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DS | SA200DS | sa20 0ds | sa200ds | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1419 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276962 | 234329 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DT | SA200DT | sa20 0dt | sa200dt | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 921 | 1359 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.33 | 13.51 | 14.93 | 276169 | 234100 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DU | SA200DU | sa20 0du | sa200du | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1818 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276618 | 234931 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DW | SA200DW | sa20 0dw | sa200dw | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1687 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276898 | 234682 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DX | SA200DX | sa20 0dx | sa200dx | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 399 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 276431 | 232918 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DY | SA200DY | sa20 0dy | sa200dy | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1670 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276576 | 234789 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0DZ | SA200DZ | sa20 0dz | sa200dz | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 659 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 275836 | 232590 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EA | SA200EA | sa20 0ea | sa200ea | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1602 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276625 | 234703 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EB | SA200EB | sa20 0eb | sa200eb | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1477 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276561 | 234592 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0ED | SA200ED | sa20 0ed | sa200ed | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1466 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 276489 | 234601 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EE | SA200EE | sa20 0ee | sa200ee | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1383 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 276484 | 234517 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EG | SA200EG | sa20 0eg | sa200eg | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1395 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 276367 | 234554 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EH | SA200EH | sa20 0eh | sa200eh | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1486 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 276268 | 234659 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EJ | SA200EJ | sa20 0ej | sa200ej | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 3023 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 273709 | 231370 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EL | SA200EL | sa20 0el | sa200el | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2456 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 275926 | 235627 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EN | SA200EN | sa20 0en | sa200en | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 3120 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 275840 | 236286 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EP | SA200EP | sa20 0ep | sa200ep | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1443 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 275564 | 234507 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EQ | SA200EQ | sa20 0eq | sa200eq | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1987 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 274690 | 231812 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0ES | SA200ES | sa20 0es | sa200es | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 894 | 1400 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.09 | 13.92 | 15.38 | 275392 | 233685 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0ET | SA200ET | sa20 0et | sa200et | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1678 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 274458 | 233041 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EU | SA200EU | sa20 0eu | sa200eu | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 3064 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 273166 | 233953 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EW | SA200EW | sa20 0ew | sa200ew | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 2942 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 275521 | 236688 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EX | SA200EX | sa20 0ex | sa200ex | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 3079 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 274242 | 230748 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EY | SA200EY | sa20 0ey | sa200ey | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 3160 | 1467 | 1200to1500 | 2.94 | 2.15 | 1.58 | 27.34 | 14.58 | 16.12 | 273620 | 235099 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0EZ | SA200EZ | sa20 0ez | sa200ez | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2507 | 1244 | 1200to1500 | 2.49 | 1.82 | 1.34 | 23.19 | 12.37 | 13.67 | 275073 | 230907 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0FA | SA200FA | sa20 0fa | sa200fa | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 6457 | 1764 | Over1500 | 3.53 | 2.58 | 1.89 | 32.88 | 17.54 | 19.38 | 273176 | 247490 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0FG | SA200FG | sa20 0fg | sa200fg | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1460 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 276410 | 234613 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0GA | SA200GA | sa20 0ga | sa200ga | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1593 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276962 | 234538 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HA | SA200HA | sa20 0ha | sa200ha | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1964 | 1416 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.39 | 14.08 | 15.56 | 274757 | 234584 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HB | SA200HB | sa20 0hb | sa200hb | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2217 | 1416 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.39 | 14.08 | 15.56 | 275048 | 235114 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HD | SA200HD | sa20 0hd | sa200hd | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2499 | 1416 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.39 | 14.08 | 15.56 | 275194 | 235496 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HE | SA200HE | sa20 0he | sa200he | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2936 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 274399 | 235551 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HF | SA200HF | sa20 0hf | sa200hf | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 3537 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 274316 | 236279 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HG | SA200HG | sa20 0hg | sa200hg | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 4040 | 1465 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.31 | 14.56 | 16.1 | 273114 | 235866 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HH | SA200HH | sa20 0hh | sa200hh | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 3953 | 1465 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.31 | 14.56 | 16.1 | 273370 | 236268 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HJ | SA200HJ | sa20 0hj | sa200hj | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2000 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 275610 | 231249 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HL | SA200HL | sa20 0hl | sa200hl | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 2658 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 274608 | 237108 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HN | SA200HN | sa20 0hn | sa200hn | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 2847 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 274151 | 237096 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HP | SA200HP | sa20 0hp | sa200hp | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 3630 | 1486 | 1200to1500 | 2.97 | 2.18 | 1.6 | 27.7 | 14.77 | 16.33 | 272951 | 236997 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HQ | SA200HQ | sa20 0hq | sa200hq | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1558 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 275315 | 231852 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HR | SA200HR | sa20 0hr | sa200hr | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 2510 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 274784 | 237210 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HS | SA200HS | sa20 0hs | sa200hs | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1382 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 276271 | 234554 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HU | SA200HU | sa20 0hu | sa200hu | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1888 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276736 | 234968 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HW | SA200HW | sa20 0hw | sa200hw | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 2990 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 273633 | 237255 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HX | SA200HX | sa20 0hx | sa200hx | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1875 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 276117 | 231305 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HY | SA200HY | sa20 0hy | sa200hy | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1801 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276796 | 234853 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0HZ | SA200HZ | sa20 0hz | sa200hz | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 1583 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 276359 | 230821 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0JB | SA200JB | sa20 0jb | sa200jb | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 1357 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 276804 | 230905 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0JD | SA200JD | sa20 0jd | sa200jd | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 513 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 277185 | 230137 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0JE | SA200JE | sa20 0je | sa200je | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 878 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 276729 | 230110 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0JF | SA200JF | sa20 0jf | sa200jf | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 1547 | 1288 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.01 | 12.8 | 14.15 | 276004 | 229541 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0JG | SA200JG | sa20 0jg | sa200jg | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 728 | 1392 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.94 | 13.84 | 15.29 | 276890 | 229425 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0JH | SA200JH | sa20 0jh | sa200jh | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 2739 | 1346 | 1200to1500 | 2.69 | 1.97 | 1.45 | 25.09 | 13.38 | 14.79 | 275176 | 228371 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0JP | SA200JP | sa20 0jp | sa200jp | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1470 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276740 | 234517 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0JQ | SA200JQ | sa20 0jq | sa200jq | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 1325 | 1392 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.94 | 13.84 | 15.29 | 276690 | 228742 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0JR | SA200JR | sa20 0jr | sa200jr | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1413 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276763 | 234443 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0JT | SA200JT | sa20 0jt | sa200jt | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1559 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 277409 | 234070 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0JU | SA200JU | sa20 0ju | sa200ju | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1977 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 277831 | 234187 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0JW | SA200JW | sa20 0jw | sa200jw | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1573 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276700 | 234646 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0JX | SA200JX | sa20 0jx | sa200jx | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2142 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 278023 | 234181 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0JY | SA200JY | sa20 0jy | sa200jy | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 3344 | 1330 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.79 | 13.22 | 14.61 | 279468 | 232998 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0JZ | SA200JZ | sa20 0jz | sa200jz | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2578 | 1330 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.79 | 13.22 | 14.61 | 278688 | 233493 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0LA | SA200LA | sa20 0la | sa200la | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1798 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276730 | 234875 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LD | SA200LD | sa20 0ld | sa200ld | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 2112 | 1396 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26.02 | 13.88 | 15.34 | 279537 | 237892 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LE | SA200LE | sa20 0le | sa200le | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 830 | 1402 | 1200to1500 | 2.81 | 2.05 | 1.51 | 26.13 | 13.94 | 15.4 | 279986 | 239102 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LF | SA200LF | sa20 0lf | sa200lf | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 710 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 280598 | 239123 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LG | SA200LG | sa20 0lg | sa200lg | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 517 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 280920 | 239682 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LH | SA200LH | sa20 0lh | sa200lh | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 479 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 280832 | 240053 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LJ | SA200LJ | sa20 0lj | sa200lj | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1470 | 1284 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.93 | 12.76 | 14.11 | 277593 | 233325 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LL | SA200LL | sa20 0ll | sa200ll | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 574 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 280721 | 240298 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LN | SA200LN | sa20 0ln | sa200ln | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 1513 | 1450 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.03 | 14.41 | 15.93 | 281057 | 241182 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LP | SA200LP | sa20 0lp | sa200lp | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 2599 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 282536 | 241316 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LQ | SA200LQ | sa20 0lq | sa200lq | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1525 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 277489 | 233872 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LR | SA200LR | sa20 0lr | sa200lr | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 262 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 280618 | 239980 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LS | SA200LS | sa20 0ls | sa200ls | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 395 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 280247 | 240166 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LT | SA200LT | sa20 0lt | sa200lt | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 403 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 280182 | 240136 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LU | SA200LU | sa20 0lu | sa200lu | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 1613 | 1448 | 1200to1500 | 2.9 | 2.12 | 1.56 | 26.99 | 14.39 | 15.91 | 279220 | 240888 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LW | SA200LW | sa20 0lw | sa200lw | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 2146 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 281152 | 241826 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LX | SA200LX | sa20 0lx | sa200lx | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1686 | 1284 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.93 | 12.76 | 14.11 | 277815 | 233239 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0LY | SA200LY | sa20 0ly | sa200ly | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 739 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 280086 | 240470 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0LZ | SA200LZ | sa20 0lz | sa200lz | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1543 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 277476 | 232426 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0NA | SA200NA | sa20 0na | sa200na | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 1088 | 1448 | 1200to1500 | 2.9 | 2.12 | 1.56 | 26.99 | 14.39 | 15.91 | 280177 | 240871 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NB | SA200NB | sa20 0nb | sa200nb | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 2032 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 280031 | 243167 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NG | SA200NG | sa20 0ng | sa200ng | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 2356 | 1493 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.83 | 14.84 | 16.4 | 277477 | 240828 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NH | SA200NH | sa20 0nh | sa200nh | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 1604 | 1521 | Over1500 | 3.04 | 2.23 | 1.63 | 28.35 | 15.12 | 16.71 | 279238 | 242180 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NJ | SA200NJ | sa20 0nj | sa200nj | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 702 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 277525 | 230464 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0NL | SA200NL | sa20 0nl | sa200nl | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 1079 | 1521 | Over1500 | 3.04 | 2.23 | 1.63 | 28.35 | 15.12 | 16.71 | 278637 | 242329 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NN | SA200NN | sa20 0nn | sa200nn | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 685 | 1599 | Over1500 | 3.2 | 2.34 | 1.72 | 29.8 | 15.89 | 17.57 | 278507 | 243661 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NP | SA200NP | sa20 0np | sa200np | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 823 | 1599 | Over1500 | 3.2 | 2.34 | 1.72 | 29.8 | 15.89 | 17.57 | 278579 | 243784 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NQ | SA200NQ | sa20 0nq | sa200nq | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1819 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 277026 | 231597 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NR | SA200NR | sa20 0nr | sa200nr | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 569 | 1622 | Over1500 | 3.25 | 2.38 | 1.74 | 30.23 | 16.12 | 17.82 | 278360 | 243641 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NS | SA200NS | sa20 0ns | sa200ns | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 482 | 1622 | Over1500 | 3.25 | 2.38 | 1.74 | 30.23 | 16.12 | 17.82 | 278109 | 243669 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NT | SA200NT | sa20 0nt | sa200nt | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 700 | 1518 | Over1500 | 3.04 | 2.22 | 1.63 | 28.29 | 15.09 | 16.68 | 277300 | 243187 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NU | SA200NU | sa20 0nu | sa200nu | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 1130 | 1518 | Over1500 | 3.04 | 2.22 | 1.63 | 28.29 | 15.09 | 16.68 | 276935 | 242824 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NW | SA200NW | sa20 0nw | sa200nw | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 867 | 1599 | Over1500 | 3.2 | 2.34 | 1.72 | 29.8 | 15.89 | 17.57 | 278579 | 243845 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NX | SA200NX | sa20 0nx | sa200nx | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 458 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 277283 | 230144 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0NY | SA200NY | sa20 0ny | sa200ny | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 721 | 1622 | Over1500 | 3.25 | 2.38 | 1.74 | 30.23 | 16.12 | 17.82 | 278481 | 243737 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0NZ | SA200NZ | sa20 0nz | sa200nz | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 441 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 277205 | 230054 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0PA | SA200PA | sa20 0pa | sa200pa | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 745 | 1622 | Over1500 | 3.25 | 2.38 | 1.74 | 30.23 | 16.12 | 17.82 | 277953 | 243943 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PB | SA200PB | sa20 0pb | sa200pb | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 1480 | 1652 | Over1500 | 3.31 | 2.42 | 1.77 | 30.79 | 16.42 | 18.15 | 277493 | 244590 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PD | SA200PD | sa20 0pd | sa200pd | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 1653 | 1652 | Over1500 | 3.31 | 2.42 | 1.77 | 30.79 | 16.42 | 18.15 | 277228 | 244661 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PE | SA200PE | sa20 0pe | sa200pe | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 1404 | 1619 | Over1500 | 3.24 | 2.37 | 1.74 | 30.18 | 16.09 | 17.79 | 276938 | 244118 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PF | SA200PF | sa20 0pf | sa200pf | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 2833 | 1666 | Over1500 | 3.33 | 2.44 | 1.79 | 31.05 | 16.56 | 18.3 | 277040 | 245865 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PG | SA200PG | sa20 0pg | sa200pg | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 3508 | 1757 | Over1500 | 3.52 | 2.57 | 1.89 | 32.75 | 17.47 | 19.3 | 278777 | 246620 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PH | SA200PH | sa20 0ph | sa200ph | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 2948 | 1666 | Over1500 | 3.33 | 2.44 | 1.79 | 31.05 | 16.56 | 18.3 | 277260 | 246053 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PJ | SA200PJ | sa20 0pj | sa200pj | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 280 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 277760 | 229596 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0PL | SA200PL | sa20 0pl | sa200pl | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 4336 | 1736 | Over1500 | 3.47 | 2.54 | 1.86 | 32.36 | 17.26 | 19.07 | 277001 | 247418 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PN | SA200PN | sa20 0pn | sa200pn | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 4162 | 1686 | Over1500 | 3.37 | 2.47 | 1.81 | 31.42 | 16.76 | 18.52 | 274955 | 246036 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PP | SA200PP | sa20 0pp | sa200pp | Carmarthenshire | Sir Gaerfyrddin | Farmers STW | 7143 | 1657 | Over1500 | 3.32 | 2.43 | 1.78 | 30.88 | 16.47 | 18.21 | 271394 | 247294 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PQ | SA200PQ | sa20 0pq | sa200pq | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 131 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 277451 | 229863 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0PR | SA200PR | sa20 0pr | sa200pr | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1361 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276937 | 234276 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PT | SA200PT | sa20 0pt | sa200pt | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1383 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276816 | 234381 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PU | SA200PU | sa20 0pu | sa200pu | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1404 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 276893 | 234358 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PW | SA200PW | sa20 0pw | sa200pw | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 3557 | 1692 | Over1500 | 3.39 | 2.48 | 1.82 | 31.54 | 16.82 | 18.59 | 275664 | 245882 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0PX | SA200PX | sa20 0px | sa200px | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 1045 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 278273 | 229022 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0PZ | SA200PZ | sa20 0pz | sa200pz | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 516 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 277437 | 230268 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0QA | SA200QA | sa20 0qa | sa200qa | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 2301 | 1442 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.88 | 14.33 | 15.84 | 279707 | 230521 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0QB | SA200QB | sa20 0qb | sa200qb | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 1721 | 1345 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.07 | 13.37 | 14.78 | 278348 | 231278 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0QD | SA200QD | sa20 0qd | sa200qd | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 2884 | 1363 | 1200to1500 | 2.73 | 2 | 1.46 | 25.4 | 13.55 | 14.98 | 279410 | 231952 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0QE | SA200QE | sa20 0qe | sa200qe | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 2747 | 1442 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.88 | 14.33 | 15.84 | 279989 | 230996 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0QF | SA200QF | sa20 0qf | sa200qf | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 4206 | 1534 | Over1500 | 3.07 | 2.25 | 1.65 | 28.59 | 15.25 | 16.85 | 281480 | 231219 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0RA | SA200RA | sa20 0ra | sa200ra | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1745 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 277347 | 234430 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RB | SA200RB | sa20 0rb | sa200rb | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1811 | 1307 | 1200to1500 | 2.62 | 1.91 | 1.4 | 24.36 | 12.99 | 14.36 | 277377 | 234493 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RD | SA200RD | sa20 0rd | sa200rd | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2123 | 1334 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.86 | 13.26 | 14.66 | 277837 | 234441 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RE | SA200RE | sa20 0re | sa200re | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2516 | 1342 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.01 | 13.34 | 14.74 | 277991 | 234872 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RF | SA200RF | sa20 0rf | sa200rf | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2927 | 1362 | 1200to1500 | 2.73 | 1.99 | 1.46 | 25.39 | 13.54 | 14.96 | 278578 | 234784 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RG | SA200RG | sa20 0rg | sa200rg | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 4209 | 1385 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.81 | 13.77 | 15.22 | 279577 | 235593 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RH | SA200RH | sa20 0rh | sa200rh | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 4575 | 1372 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.57 | 13.64 | 15.07 | 280455 | 235236 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RL | SA200RL | sa20 0rl | sa200rl | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 3755 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 282151 | 236479 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RN | SA200RN | sa20 0rn | sa200rn | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 4584 | 1393 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.96 | 13.85 | 15.3 | 281703 | 235411 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RP | SA200RP | sa20 0rp | sa200rp | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 5360 | 1431 | 1200to1500 | 2.86 | 2.1 | 1.54 | 26.67 | 14.22 | 15.72 | 283467 | 235402 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RR | SA200RR | sa20 0rr | sa200rr | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 5647 | 1431 | 1200to1500 | 2.86 | 2.1 | 1.54 | 26.67 | 14.22 | 15.72 | 282565 | 234588 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RS | SA200RS | sa20 0rs | sa200rs | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 5904 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 282178 | 234175 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RT | SA200RT | sa20 0rt | sa200rt | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 4596 | 1372 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.57 | 13.64 | 15.07 | 280322 | 235061 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RU | SA200RU | sa20 0ru | sa200ru | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 4730 | 1365 | 1200to1500 | 2.73 | 2 | 1.47 | 25.44 | 13.57 | 15 | 280813 | 233841 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0RW | SA200RW | sa20 0rw | sa200rw | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 4891 | 1427 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.6 | 14.19 | 15.68 | 282833 | 235558 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0RY | SA200RY | sa20 0ry | sa200ry | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 5711 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 281963 | 233366 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0SA | SA200SA | sa20 0sa | sa200sa | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 6197 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 282587 | 233349 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0SB | SA200SB | sa20 0sb | sa200sb | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 5780 | 1427 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.6 | 14.19 | 15.68 | 283984 | 235262 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0SD | SA200SD | sa20 0sd | sa200sd | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 6197 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 282899 | 232862 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0SE | SA200SE | sa20 0se | sa200se | Carmarthenshire | Sir Gaerfyrddin | Trecastle WwTW | 6115 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 283425 | 232889 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0SF | SA200SF | sa20 0sf | sa200sf | Carmarthenshire | Sir Gaerfyrddin | Myddfai WwTW | 5502 | 1493 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.83 | 14.84 | 16.4 | 282412 | 232306 | Brecon Beacons National Park LPA | CA | Afon Tywi/ River Tywi | Parc Cenedlaethol Bannau Brycheiniog | Bannau Brycheiniog National Park
SA20 0SN | SA200SN | sa20 0sn | sa200sn | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 1593 | 1432 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.69 | 14.23 | 15.73 | 275338 | 238040 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0SP | SA200SP | sa20 0sp | sa200sp | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 191 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 275288 | 239730 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0SR | SA200SR | sa20 0sr | sa200sr | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 256 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 275295 | 239833 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0SS | SA200SS | sa20 0ss | sa200ss | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 473 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 275284 | 240072 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0ST | SA200ST | sa20 0st | sa200st | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 462 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 275315 | 240071 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0SU | SA200SU | sa20 0su | sa200su | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 573 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 275275 | 240174 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0SW | SA200SW | sa20 0sw | sa200sw | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 784 | 1422 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.5 | 14.14 | 15.62 | 275909 | 238993 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0SY | SA200SY | sa20 0sy | sa200sy | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 526 | 1459 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.19 | 14.5 | 16.03 | 275150 | 239197 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TA | SA200TA | sa20 0ta | sa200ta | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 314 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 275156 | 239739 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TB | SA200TB | sa20 0tb | sa200tb | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 1305 | 1536 | Over1500 | 3.07 | 2.25 | 1.65 | 28.63 | 15.27 | 16.88 | 274434 | 238810 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TD | SA200TD | sa20 0td | sa200td | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 1551 | 1432 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.69 | 14.23 | 15.73 | 274892 | 238182 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TE | SA200TE | sa20 0te | sa200te | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 2105 | 1536 | Over1500 | 3.07 | 2.25 | 1.65 | 28.63 | 15.27 | 16.88 | 273599 | 238627 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TF | SA200TF | sa20 0tf | sa200tf | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 1193 | 1569 | Over1500 | 3.14 | 2.3 | 1.69 | 29.24 | 15.6 | 17.24 | 275027 | 240744 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TG | SA200TG | sa20 0tg | sa200tg | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 2292 | 1648 | Over1500 | 3.3 | 2.41 | 1.77 | 30.72 | 16.38 | 18.11 | 275462 | 241920 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TH | SA200TH | sa20 0th | sa200th | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 2248 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 276075 | 242040 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TL | SA200TL | sa20 0tl | sa200tl | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 1416 | 1495 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.86 | 14.86 | 16.43 | 276800 | 242448 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TN | SA200TN | sa20 0tn | sa200tn | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 1503 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 274082 | 240251 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TT | SA200TT | sa20 0tt | sa200tt | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2284 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 276442 | 235442 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TU | SA200TU | sa20 0tu | sa200tu | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 3020 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 276260 | 236197 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TW | SA200TW | sa20 0tw | sa200tw | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 2159 | 1597 | Over1500 | 3.2 | 2.34 | 1.72 | 29.77 | 15.87 | 17.55 | 273344 | 239156 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0TY | SA200TY | sa20 0ty | sa200ty | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 2460 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 276394 | 237358 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UA | SA200UA | sa20 0ua | sa200ua | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 1925 | 1432 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.69 | 14.23 | 15.73 | 275467 | 237704 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UB | SA200UB | sa20 0ub | sa200ub | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 1490 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 276931 | 239792 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UD | SA200UD | sa20 0ud | sa200ud | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 1009 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 276437 | 239837 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UE | SA200UE | sa20 0ue | sa200ue | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 952 | 1514 | Over1500 | 3.03 | 2.22 | 1.63 | 28.22 | 15.05 | 16.63 | 276248 | 240148 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UF | SA200UF | sa20 0uf | sa200uf | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 1621 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 276172 | 241080 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UG | SA200UG | sa20 0ug | sa200ug | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 1211 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 276595 | 240022 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UH | SA200UH | sa20 0uh | sa200uh | Carmarthenshire | Sir Gaerfyrddin | Rhandirmwyn STW | 1736 | 1495 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.86 | 14.86 | 16.43 | 277072 | 241733 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UL | SA200UL | sa20 0ul | sa200ul | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 1714 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 277133 | 239950 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UN | SA200UN | sa20 0un | sa200un | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 2291 | 1487 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.72 | 14.78 | 16.34 | 278340 | 240771 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UP | SA200UP | sa20 0up | sa200up | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 1489 | 1429 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.63 | 14.2 | 15.7 | 278954 | 240077 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UR | SA200UR | sa20 0ur | sa200ur | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 1916 | 1388 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.87 | 13.8 | 15.25 | 278967 | 238561 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0US | SA200US | sa20 0us | sa200us | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 2490 | 1401 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.11 | 13.93 | 15.39 | 278173 | 238736 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UT | SA200UT | sa20 0ut | sa200ut | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 2824 | 1395 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26 | 13.87 | 15.33 | 278165 | 238109 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UU | SA200UU | sa20 0uu | sa200uu | Carmarthenshire | Sir Gaerfyrddin | Cilycwm WwTW | 3555 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 277358 | 236630 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0UW | SA200UW | sa20 0uw | sa200uw | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 1804 | 1429 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.63 | 14.2 | 15.7 | 278653 | 240175 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YD | SA200YD | sa20 0yd | sa200yd | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1495 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276797 | 234518 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YE | SA200YE | sa20 0ye | sa200ye | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1547 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276734 | 234604 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YF | SA200YF | sa20 0yf | sa200yf | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2055 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276909 | 235081 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YG | SA200YG | sa20 0yg | sa200yg | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 2676 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 277408 | 235530 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YH | SA200YH | sa20 0yh | sa200yh | Carmarthenshire | Sir Gaerfyrddin | Llandovery WwTW | 1501 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 276776 | 234534 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YL | SA200YL | sa20 0yl | sa200yl | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 3888 | 1372 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.57 | 13.64 | 15.07 | 278725 | 236311 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YN | SA200YN | sa20 0yn | sa200yn | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 3395 | 1385 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.81 | 13.77 | 15.22 | 280172 | 236425 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YP | SA200YP | sa20 0yp | sa200yp | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 2319 | 1396 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26.02 | 13.88 | 15.34 | 279767 | 237585 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YR | SA200YR | sa20 0yr | sa200yr | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 1245 | 1424 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.54 | 14.16 | 15.65 | 281027 | 238724 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YS | SA200YS | sa20 0ys | sa200ys | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 2117 | 1525 | Over1500 | 3.05 | 2.23 | 1.64 | 28.42 | 15.16 | 16.75 | 282532 | 239681 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YT | SA200YT | sa20 0yt | sa200yt | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 1822 | 1533 | Over1500 | 3.07 | 2.25 | 1.65 | 28.57 | 15.24 | 16.84 | 282091 | 240532 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YU | SA200YU | sa20 0yu | sa200yu | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 3562 | 1563 | Over1500 | 3.13 | 2.29 | 1.68 | 29.13 | 15.54 | 17.17 | 283858 | 238886 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA20 0YW | SA200YW | sa20 0yw | sa200yw | Carmarthenshire | Sir Gaerfyrddin | Cynghordy WwTW | 2724 | 1340 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.98 | 13.32 | 14.72 | 279429 | 237273 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1AD | SA311AD | sa31 1ad | sa311ad | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3750 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241301 | 219986 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1AF | SA311AF | sa31 1af | sa311af | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3301 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241055 | 220489 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1AG | SA311AG | sa31 1ag | sa311ag | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3406 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241667 | 220298 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1AH | SA311AH | sa31 1ah | sa311ah | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3275 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241469 | 220444 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1AN | SA311AN | sa31 1an | sa311an | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3670 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241295 | 220068 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1AS | SA311AS | sa31 1as | sa311as | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3000 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241432 | 220725 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1AW | SA311AW | sa31 1aw | sa311aw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3588 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241248 | 220158 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1BA | SA311BA | sa31 1ba | sa311ba | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3678 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241289 | 220061 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1BD | SA311BD | sa31 1bd | sa311bd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3647 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241321 | 220088 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1BH | SA311BH | sa31 1bh | sa311bh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3599 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241389 | 220127 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1BS | SA311BS | sa31 1bs | sa311bs | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3520 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241438 | 220201 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1BU | SA311BU | sa31 1bu | sa311bu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3576 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241318 | 220160 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1BW | SA311BW | sa31 1bw | sa311bw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3569 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241389 | 220157 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1BX | SA311BX | sa31 1bx | sa311bx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3502 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241410 | 220222 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1BY | SA311BY | sa31 1by | sa311by | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3549 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241291 | 220191 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DA | SA311DA | sa31 1da | sa311da | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3454 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241358 | 220277 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DB | SA311DB | sa31 1db | sa311db | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3430 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241274 | 220314 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DD | SA311DD | sa31 1dd | sa311dd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3449 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241216 | 220305 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DE | SA311DE | sa31 1de | sa311de | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3455 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241170 | 220307 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DG | SA311DG | sa31 1dg | sa311dg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3413 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241193 | 220345 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DH | SA311DH | sa31 1dh | sa311dh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3336 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241208 | 220421 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DJ | SA311DJ | sa31 1dj | sa311dj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3404 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241142 | 220365 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DL | SA311DL | sa31 1dl | sa311dl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3238 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241189 | 220524 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DN | SA311DN | sa31 1dn | sa311dn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3088 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241109 | 220695 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DP | SA311DP | sa31 1dp | sa311dp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3094 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241144 | 220681 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DQ | SA311DQ | sa31 1dq | sa311dq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3329 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241140 | 220441 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DR | SA311DR | sa31 1dr | sa311dr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3122 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241067 | 220670 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DS | SA311DS | sa31 1ds | sa311ds | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3129 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241265 | 220621 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DU | SA311DU | sa31 1du | sa311du | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3035 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241247 | 220720 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DX | SA311DX | sa31 1dx | sa311dx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3270 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241282 | 220475 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DY | SA311DY | sa31 1dy | sa311dy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3313 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241234 | 220440 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1DZ | SA311DZ | sa31 1dz | sa311dz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2944 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241405 | 220786 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1EA | SA311EA | sa31 1ea | sa311ea | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2689 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241429 | 221040 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1EB | SA311EB | sa31 1eb | sa311eb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2738 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241710 | 220964 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1ED | SA311ED | sa31 1ed | sa311ed | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2769 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241636 | 220937 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1EE | SA311EE | sa31 1ee | sa311ee | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2673 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241320 | 221074 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1EF | SA311EF | sa31 1ef | sa311ef | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2682 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241770 | 221019 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1EG | SA311EG | sa31 1eg | sa311eg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2453 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241621 | 221255 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1EH | SA311EH | sa31 1eh | sa311eh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2812 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241622 | 220895 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1EJ | SA311EJ | sa31 1ej | sa311ej | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2896 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241693 | 220807 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1ER | SA311ER | sa31 1er | sa311er | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3435 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241400 | 220291 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1ET | SA311ET | sa31 1et | sa311et | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3546 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241586 | 220162 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1EU | SA311EU | sa31 1eu | sa311eu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3371 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241413 | 220354 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1EX | SA311EX | sa31 1ex | sa311ex | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3326 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241382 | 220403 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1EY | SA311EY | sa31 1ey | sa311ey | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3400 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241268 | 220345 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1EZ | SA311EZ | sa31 1ez | sa311ez | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3319 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241318 | 220419 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1GA | SA311GA | sa31 1ga | sa311ga | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3472 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241095 | 220305 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1GW | SA311GW | sa31 1gw | sa311gw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3498 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241622 | 220208 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1GX | SA311GX | sa31 1gx | sa311gx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2820 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242094 | 220894 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1GY | SA311GY | sa31 1gy | sa311gy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3273 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241423 | 220451 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1GZ | SA311GZ | sa31 1gz | sa311gz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2885 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241472 | 220836 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HA | SA311HA | sa31 1ha | sa311ha | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3354 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241339 | 220381 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HB | SA311HB | sa31 1hb | sa311hb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3395 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241320 | 220342 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HD | SA311HD | sa31 1hd | sa311hd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3293 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241383 | 220436 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HE | SA311HE | sa31 1he | sa311he | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3214 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241502 | 220502 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HF | SA311HF | sa31 1hf | sa311hf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3152 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241562 | 220559 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HG | SA311HG | sa31 1hg | sa311hg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3141 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241621 | 220566 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HH | SA311HH | sa31 1hh | sa311hh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3118 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241635 | 220588 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HJ | SA311HJ | sa31 1hj | sa311hj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3110 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241590 | 220599 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HL | SA311HL | sa31 1hl | sa311hl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3058 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241447 | 220665 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HN | SA311HN | sa31 1hn | sa311hn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3008 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241532 | 220706 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HP | SA311HP | sa31 1hp | sa311hp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3049 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241727 | 220653 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HQ | SA311HQ | sa31 1hq | sa311hq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3127 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241604 | 220581 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HR | SA311HR | sa31 1hr | sa311hr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2950 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241981 | 220755 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HT | SA311HT | sa31 1ht | sa311ht | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2885 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241992 | 220820 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HU | SA311HU | sa31 1hu | sa311hu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2901 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241927 | 220801 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HW | SA311HW | sa31 1hw | sa311hw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3045 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241562 | 220666 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HX | SA311HX | sa31 1hx | sa311hx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2720 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241972 | 220985 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HY | SA311HY | sa31 1hy | sa311hy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2766 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241953 | 220937 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1HZ | SA311HZ | sa31 1hz | sa311hz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3266 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241616 | 220441 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JA | SA311JA | sa31 1ja | sa311ja | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2888 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241839 | 220812 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JB | SA311JB | sa31 1jb | sa311jb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2945 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241617 | 220762 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JD | SA311JD | sa31 1jd | sa311jd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2969 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241610 | 220739 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JE | SA311JE | sa31 1je | sa311je | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2894 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241893 | 220807 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JF | SA311JF | sa31 1jf | sa311jf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2977 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241689 | 220726 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JG | SA311JG | sa31 1jg | sa311jg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2949 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241885 | 220752 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JJ | SA311JJ | sa31 1jj | sa311jj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2718 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241857 | 220983 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JL | SA311JL | sa31 1jl | sa311jl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2800 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241831 | 220900 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JN | SA311JN | sa31 1jn | sa311jn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3758 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241461 | 219960 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JP | SA311JP | sa31 1jp | sa311jp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3778 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241336 | 219953 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JQ | SA311JQ | sa31 1jq | sa311jq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3023 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241692 | 220680 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JR | SA311JR | sa31 1jr | sa311jr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3691 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241352 | 220039 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JT | SA311JT | sa31 1jt | sa311jt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3707 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241347 | 220024 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JU | SA311JU | sa31 1ju | sa311ju | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3533 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241551 | 220178 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JW | SA311JW | sa31 1jw | sa311jw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3763 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241416 | 219959 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1JY | SA311JY | sa31 1jy | sa311jy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3625 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241455 | 220094 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LD | SA311LD | sa31 1ld | sa311ld | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3558 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241465 | 220160 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LE | SA311LE | sa31 1le | sa311le | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3715 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241409 | 220008 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LG | SA311LG | sa31 1lg | sa311lg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3651 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241444 | 220069 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LH | SA311LH | sa31 1lh | sa311lh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3527 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241479 | 220190 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LL | SA311LL | sa31 1ll | sa311ll | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3598 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241517 | 220115 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LN | SA311LN | sa31 1ln | sa311ln | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3453 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241525 | 220260 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LP | SA311LP | sa31 1lp | sa311lp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3676 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241539 | 220035 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LQ | SA311LQ | sa31 1lq | sa311lq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3584 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241451 | 220135 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LR | SA311LR | sa31 1lr | sa311lr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3419 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241596 | 220289 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LS | SA311LS | sa31 1ls | sa311ls | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3454 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241595 | 220254 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LU | SA311LU | sa31 1lu | sa311lu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3401 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241707 | 220301 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LW | SA311LW | sa31 1lw | sa311lw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3448 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241721 | 220254 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LX | SA311LX | sa31 1lx | sa311lx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3387 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241730 | 220315 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LY | SA311LY | sa31 1ly | sa311ly | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3522 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241666 | 220182 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1LZ | SA311LZ | sa31 1lz | sa311lz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3451 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241765 | 220250 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NA | SA311NA | sa31 1na | sa311na | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3355 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241675 | 220348 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NB | SA311NB | sa31 1nb | sa311nb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3264 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241724 | 220438 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1ND | SA311ND | sa31 1nd | sa311nd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3251 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241716 | 220451 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NE | SA311NE | sa31 1ne | sa311ne | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3237 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241778 | 220464 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NF | SA311NF | sa31 1nf | sa311nf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3255 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241776 | 220446 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NG | SA311NG | sa31 1ng | sa311ng | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3360 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241848 | 220340 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NH | SA311NH | sa31 1nh | sa311nh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3344 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241786 | 220356 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NJ | SA311NJ | sa31 1nj | sa311nj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3317 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241902 | 220384 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NL | SA311NL | sa31 1nl | sa311nl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3305 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241940 | 220397 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NN | SA311NN | sa31 1nn | sa311nn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3126 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241929 | 220576 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NP | SA311NP | sa31 1np | sa311np | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3207 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241865 | 220494 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NQ | SA311NQ | sa31 1nq | sa311nq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3395 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241813 | 220305 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NR | SA311NR | sa31 1nr | sa311nr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3099 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242121 | 220616 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NS | SA311NS | sa31 1ns | sa311ns | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3106 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242021 | 220601 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NT | SA311NT | sa31 1nt | sa311nt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3071 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242064 | 220639 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NU | SA311NU | sa31 1nu | sa311nu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3117 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241902 | 220584 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NW | SA311NW | sa31 1nw | sa311nw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3089 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242030 | 220618 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NX | SA311NX | sa31 1nx | sa311nx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3160 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241811 | 220540 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NY | SA311NY | sa31 1ny | sa311ny | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3141 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241762 | 220560 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1NZ | SA311NZ | sa31 1nz | sa311nz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3108 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241971 | 220596 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PA | SA311PA | sa31 1pa | sa311pa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3298 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241695 | 220405 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PB | SA311PB | sa31 1pb | sa311pb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3310 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241685 | 220393 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PD | SA311PD | sa31 1pd | sa311pd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3277 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241648 | 220428 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PE | SA311PE | sa31 1pe | sa311pe | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3292 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241665 | 220412 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PF | SA311PF | sa31 1pf | sa311pf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3298 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241658 | 220406 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PG | SA311PG | sa31 1pg | sa311pg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3711 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241261 | 220032 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PH | SA311PH | sa31 1ph | sa311ph | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3722 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241246 | 220023 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PN | SA311PN | sa31 1pn | sa311pn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3684 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241209 | 220067 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PQ | SA311PQ | sa31 1pq | sa311pq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3727 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241284 | 220012 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PR | SA311PR | sa31 1pr | sa311pr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3731 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241174 | 220026 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PS | SA311PS | sa31 1ps | sa311ps | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3698 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241119 | 220069 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PT | SA311PT | sa31 1pt | sa311pt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3720 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241123 | 220046 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PU | SA311PU | sa31 1pu | sa311pu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3658 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241046 | 220125 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PW | SA311PW | sa31 1pw | sa311pw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3670 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241168 | 220089 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PX | SA311PX | sa31 1px | sa311px | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3670 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241023 | 220118 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PY | SA311PY | sa31 1py | sa311py | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3650 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240926 | 220161 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1PZ | SA311PZ | sa31 1pz | sa311pz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3671 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240918 | 220142 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1QB | SA311QB | sa31 1qb | sa311qb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3714 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241160 | 220045 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1QD | SA311QD | sa31 1qd | sa311qd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3646 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241289 | 220093 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1QE | SA311QE | sa31 1qe | sa311qe | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3602 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241272 | 220140 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1QF | SA311QF | sa31 1qf | sa311qf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2689 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241730 | 221013 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1QG | SA311QG | sa31 1qg | sa311qg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3557 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241214 | 220195 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1QL | SA311QL | sa31 1ql | sa311ql | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3650 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241135 | 220115 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1QN | SA311QN | sa31 1qn | sa311qn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3545 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241154 | 220218 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1QP | SA311QP | sa31 1qp | sa311qp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3351 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241519 | 220363 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1QT | SA311QT | sa31 1qt | sa311qt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3514 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241160 | 220249 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1QX | SA311QX | sa31 1qx | sa311qx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3627 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241035 | 220159 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1QY | SA311QY | sa31 1qy | sa311qy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3576 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241085 | 220201 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1QZ | SA311QZ | sa31 1qz | sa311qz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3586 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241094 | 220189 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RA | SA311RA | sa31 1ra | sa311ra | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3640 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241169 | 220119 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RB | SA311RB | sa31 1rb | sa311rb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3578 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241001 | 220217 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RD | SA311RD | sa31 1rd | sa311rd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3544 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241036 | 220244 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RE | SA311RE | sa31 1re | sa311re | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3584 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240930 | 220229 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RF | SA311RF | sa31 1rf | sa311rf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3596 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240948 | 220212 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RG | SA311RG | sa31 1rg | sa311rg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3577 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240854 | 220256 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RH | SA311RH | sa31 1rh | sa311rh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3590 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240830 | 220250 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RJ | SA311RJ | sa31 1rj | sa311rj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3435 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240864 | 220401 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RL | SA311RL | sa31 1rl | sa311rl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3496 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240681 | 220395 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RN | SA311RN | sa31 1rn | sa311rn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3472 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240720 | 220407 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RP | SA311RP | sa31 1rp | sa311rp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3426 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240778 | 220437 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RQ | SA311RQ | sa31 1rq | sa311rq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3362 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240595 | 220569 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RR | SA311RR | sa31 1rr | sa311rr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3493 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240854 | 220344 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RS | SA311RS | sa31 1rs | sa311rs | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3574 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241159 | 220188 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RT | SA311RT | sa31 1rt | sa311rt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3426 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240955 | 220385 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RU | SA311RU | sa31 1ru | sa311ru | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3367 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240991 | 220437 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RW | SA311RW | sa31 1rw | sa311rw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3529 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240751 | 220337 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RX | SA311RX | sa31 1rx | sa311rx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3653 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241071 | 220125 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RY | SA311RY | sa31 1ry | sa311ry | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3351 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240887 | 220482 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1RZ | SA311RZ | sa31 1rz | sa311rz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3289 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240888 | 220546 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SA | SA311SA | sa31 1sa | sa311sa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3267 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241004 | 220537 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SB | SA311SB | sa31 1sb | sa311sb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3316 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240994 | 220489 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SD | SA311SD | sa31 1sd | sa311sd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2923 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241002 | 220894 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SE | SA311SE | sa31 1se | sa311se | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3538 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241211 | 220215 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SF | SA311SF | sa31 1sf | sa311sf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2859 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240896 | 220995 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SG | SA311SG | sa31 1sg | sa311sg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3016 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241023 | 220792 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SH | SA311SH | sa31 1sh | sa311sh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3442 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240346 | 220590 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SJ | SA311SJ | sa31 1sj | sa311sj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3430 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240610 | 220491 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SL | SA311SL | sa31 1sl | sa311sl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3282 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240556 | 220671 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SN | SA311SN | sa31 1sn | sa311sn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3332 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240398 | 220687 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SP | SA311SP | sa31 1sp | sa311sp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3440 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240106 | 220718 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SQ | SA311SQ | sa31 1sq | sa311sq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3004 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240968 | 220820 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SR | SA311SR | sa31 1sr | sa311sr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3611 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241467 | 220107 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SS | SA311SS | sa31 1ss | sa311ss | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3233 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240357 | 220817 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1ST | SA311ST | sa31 1st | sa311st | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3216 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240517 | 220760 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SU | SA311SU | sa31 1su | sa311su | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3198 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240504 | 220786 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SW | SA311SW | sa31 1sw | sa311sw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3336 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240341 | 220710 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SX | SA311SX | sa31 1sx | sa311sx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3176 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240484 | 220819 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SY | SA311SY | sa31 1sy | sa311sy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3050 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240599 | 220905 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1SZ | SA311SZ | sa31 1sz | sa311sz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2961 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240766 | 220933 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TA | SA311TA | sa31 1ta | sa311ta | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3008 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240624 | 220940 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TB | SA311TB | sa31 1tb | sa311tb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3076 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240853 | 220780 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TD | SA311TD | sa31 1td | sa311td | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3118 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240721 | 220782 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TE | SA311TE | sa31 1te | sa311te | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3187 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240896 | 220650 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TF | SA311TF | sa31 1tf | sa311tf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3185 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241020 | 220617 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TG | SA311TG | sa31 1tg | sa311tg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3230 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240924 | 220597 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TH | SA311TH | sa31 1th | sa311th | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3015 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240892 | 220832 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TJ | SA311TJ | sa31 1tj | sa311tj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3053 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240903 | 220788 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TL | SA311TL | sa31 1tl | sa311tl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3093 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240916 | 220742 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TN | SA311TN | sa31 1tn | sa311tn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3761 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241234 | 219985 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TP | SA311TP | sa31 1tp | sa311tp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3076 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241006 | 220734 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TQ | SA311TQ | sa31 1tq | sa311tq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2968 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 240875 | 220887 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TR | SA311TR | sa31 1tr | sa311tr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2702 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241131 | 221088 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TS | SA311TS | sa31 1ts | sa311ts | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2999 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 241168 | 220773 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TX | SA311TX | sa31 1tx | sa311tx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3067 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240279 | 221049 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1TY | SA311TY | sa31 1ty | sa311ty | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2472 | 1492 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.81 | 14.83 | 16.39 | 240318 | 221737 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1YF | SA311YF | sa31 1yf | sa311yf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 1ZD | SA311ZD | sa31 1zd | sa311zd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3777 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241337 | 219954 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AA | SA312AA | sa31 2aa | sa312aa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2701 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242498 | 221086 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AD | SA312AD | sa31 2ad | sa312ad | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2604 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242653 | 221233 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AE | SA312AE | sa31 2ae | sa312ae | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2508 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242742 | 221368 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AF | SA312AF | sa31 2af | sa312af | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2645 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242791 | 221240 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AH | SA312AH | sa31 2ah | sa312ah | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2458 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242774 | 221435 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AJ | SA312AJ | sa31 2aj | sa312aj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2421 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242688 | 221440 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AL | SA312AL | sa31 2al | sa312al | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2206 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 242745 | 221697 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AN | SA312AN | sa31 2an | sa312an | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2306 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 242672 | 221557 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AP | SA312AP | sa31 2ap | sa312ap | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1967 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 242744 | 221964 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AQ | SA312AQ | sa31 2aq | sa312aq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2444 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 242979 | 221548 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AR | SA312AR | sa31 2ar | sa312ar | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1799 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 242654 | 222106 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AS | SA312AS | sa31 2as | sa312as | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2398 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242639 | 221446 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AT | SA312AT | sa31 2at | sa312at | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2527 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242577 | 221289 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AU | SA312AU | sa31 2au | sa312au | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2629 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242474 | 221154 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AW | SA312AW | sa31 2aw | sa312aw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2030 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 242693 | 221868 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AX | SA312AX | sa31 2ax | sa312ax | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2595 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242564 | 221214 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AY | SA312AY | sa31 2ay | sa312ay | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2194 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 242805 | 221740 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2AZ | SA312AZ | sa31 2az | sa312az | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2157 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 242688 | 221726 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2BB | SA312BB | sa31 2bb | sa312bb | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2440 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 243941 | 220875 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2BD | SA312BD | sa31 2bd | sa312bd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3931 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241473 | 219785 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2BE | SA312BE | sa31 2be | sa312be | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3991 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241266 | 219748 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2BG | SA312BG | sa31 2bg | sa312bg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4373 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241128 | 219382 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2BH | SA312BH | sa31 2bh | sa312bh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2399 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242757 | 221492 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2BL | SA312BL | sa31 2bl | sa312bl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3995 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241776 | 219706 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2BN | SA312BN | sa31 2bn | sa312bn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3964 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241420 | 219757 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2BP | SA312BP | sa31 2bp | sa312bp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4102 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241402 | 219620 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2BR | SA312BR | sa31 2br | sa312br | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3967 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241461 | 219750 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2BS | SA312BS | sa31 2bs | sa312bs | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4190 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241388 | 219533 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2BZ | SA312BZ | sa31 2bz | sa312bz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2114 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 242838 | 221848 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DB | SA312DB | sa31 2db | sa312db | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2686 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242222 | 221045 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DD | SA312DD | sa31 2dd | sa312dd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4483 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241301 | 219248 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DE | SA312DE | sa31 2de | sa312de | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2690 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242547 | 221110 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DF | SA312DF | sa31 2df | sa312df | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2333 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 242798 | 221582 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DG | SA312DG | sa31 2dg | sa312dg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2355 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 242791 | 221555 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DJ | SA312DJ | sa31 2dj | sa312dj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4520 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241293 | 219211 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DL | SA312DL | sa31 2dl | sa312dl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4542 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241251 | 219194 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DS | SA312DS | sa31 2ds | sa312ds | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4363 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241657 | 219340 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DT | SA312DT | sa31 2dt | sa312dt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4314 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241729 | 219387 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DU | SA312DU | sa31 2du | sa312du | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4270 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241765 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DX | SA312DX | sa31 2dx | sa312dx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4268 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241831 | 219432 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DY | SA312DY | sa31 2dy | sa312dy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4331 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241924 | 219371 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2DZ | SA312DZ | sa31 2dz | sa312dz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4387 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241940 | 219315 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EA | SA312EA | sa31 2ea | sa312ea | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4380 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 242011 | 219325 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EB | SA312EB | sa31 2eb | sa312eb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4479 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 242055 | 219228 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2ED | SA312ED | sa31 2ed | sa312ed | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4366 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241834 | 219334 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EE | SA312EE | sa31 2ee | sa312ee | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4467 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241902 | 219234 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EF | SA312EF | sa31 2ef | sa312ef | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4558 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241890 | 219143 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EJ | SA312EJ | sa31 2ej | sa312ej | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2981 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242068 | 220730 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EL | SA312EL | sa31 2el | sa312el | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2939 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242046 | 220770 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EN | SA312EN | sa31 2en | sa312en | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3008 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242112 | 220706 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EP | SA312EP | sa31 2ep | sa312ep | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2845 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242220 | 220884 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2ER | SA312ER | sa31 2er | sa312er | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2696 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242133 | 221022 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2ET | SA312ET | sa31 2et | sa312et | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2535 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241963 | 221169 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EU | SA312EU | sa31 2eu | sa312eu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2535 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 241963 | 221169 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EW | SA312EW | sa31 2ew | sa312ew | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2892 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242180 | 220831 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EX | SA312EX | sa31 2ex | sa312ex | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2501 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242137 | 221219 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EY | SA312EY | sa31 2ey | sa312ey | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2770 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242325 | 220977 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2EZ | SA312EZ | sa31 2ez | sa312ez | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2683 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242310 | 221062 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HA | SA312HA | sa31 2ha | sa312ha | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2592 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242178 | 221133 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HB | SA312HB | sa31 2hb | sa312hb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2423 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242370 | 221340 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HD | SA312HD | sa31 2hd | sa312hd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2480 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242169 | 221245 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HE | SA312HE | sa31 2he | sa312he | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2664 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242373 | 221094 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HF | SA312HF | sa31 2hf | sa312hf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2808 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242662 | 221021 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HG | SA312HG | sa31 2hg | sa312hg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2745 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242701 | 221101 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HH | SA312HH | sa31 2hh | sa312hh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2951 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 243054 | 221020 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HJ | SA312HJ | sa31 2hj | sa312hj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2933 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 243090 | 221057 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HL | SA312HL | sa31 2hl | sa312hl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2393 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242212 | 221340 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HN | SA312HN | sa31 2hn | sa312hn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2602 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 242284 | 221140 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HP | SA312HP | sa31 2hp | sa312hp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2885 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 243169 | 221150 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HQ | SA312HQ | sa31 2hq | sa312hq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2785 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242705 | 221060 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HR | SA312HR | sa31 2hr | sa312hr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3924 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 242288 | 219804 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HS | SA312HS | sa31 2hs | sa312hs | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 4033 | 1392 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.94 | 13.84 | 15.29 | 242692 | 219730 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HT | SA312HT | sa31 2ht | sa312ht | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4083 | 1392 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.94 | 13.84 | 15.29 | 242598 | 219692 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HU | SA312HU | sa31 2hu | sa312hu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2914 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 242931 | 221006 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HY | SA312HY | sa31 2hy | sa312hy | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 3718 | 1392 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.94 | 13.84 | 15.29 | 242903 | 220016 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2HZ | SA312HZ | sa31 2hz | sa312hz | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2308 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 244026 | 221074 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JA | SA312JA | sa31 2ja | sa312ja | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2522 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 243819 | 221020 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JB | SA312JB | sa31 2jb | sa312jb | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2513 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 243823 | 221045 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JD | SA312JD | sa31 2jd | sa312jd | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2516 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 243808 | 221105 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JE | SA312JE | sa31 2je | sa312je | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2483 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 243880 | 220935 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JF | SA312JF | sa31 2jf | sa312jf | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1917 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 244396 | 221217 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JG | SA312JG | sa31 2jg | sa312jg | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2342 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 244012 | 220985 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JH | SA312JH | sa31 2jh | sa312jh | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2572 | 1447 | 1200to1500 | 2.9 | 2.12 | 1.55 | 26.97 | 14.38 | 15.9 | 243708 | 221540 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JJ | SA312JJ | sa31 2jj | sa312jj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2671 | 1447 | 1200to1500 | 2.9 | 2.12 | 1.55 | 26.97 | 14.38 | 15.9 | 243612 | 221679 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JL | SA312JL | sa31 2jl | sa312jl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2547 | 1447 | 1200to1500 | 2.9 | 2.12 | 1.55 | 26.97 | 14.38 | 15.9 | 243609 | 221887 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JN | SA312JN | sa31 2jn | sa312jn | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2663 | 1447 | 1200to1500 | 2.9 | 2.12 | 1.55 | 26.97 | 14.38 | 15.9 | 243618 | 221519 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JP | SA312JP | sa31 2jp | sa312jp | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2639 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 243681 | 221114 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JQ | SA312JQ | sa31 2jq | sa312jq | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2140 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 244145 | 221424 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JR | SA312JR | sa31 2jr | sa312jr | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2375 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 243957 | 221079 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JT | SA312JT | sa31 2jt | sa312jt | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2551 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 243736 | 221381 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JU | SA312JU | sa31 2ju | sa312ju | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2591 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 243693 | 221432 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JW | SA312JW | sa31 2jw | sa312jw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2193 | 1447 | 1200to1500 | 2.9 | 2.12 | 1.55 | 26.97 | 14.38 | 15.9 | 243626 | 222457 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JX | SA312JX | sa31 2jx | sa312jx | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2536 | 1391 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.93 | 13.83 | 15.28 | 243758 | 221307 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JY | SA312JY | sa31 2jy | sa312jy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4490 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241473 | 219224 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2JZ | SA312JZ | sa31 2jz | sa312jz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4606 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241827 | 219094 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2LA | SA312LA | sa31 2la | sa312la | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4466 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241635 | 219238 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2LB | SA312LB | sa31 2lb | sa312lb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4607 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 242088 | 219101 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2LD | SA312LD | sa31 2ld | sa312ld | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4466 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241800 | 219234 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2LE | SA312LE | sa31 2le | sa312le | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4547 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 242191 | 219169 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2LF | SA312LF | sa31 2lf | sa312lf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4506 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 242214 | 219212 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2LG | SA312LG | sa31 2lg | sa312lg | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 4299 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 242840 | 218992 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2LH | SA312LH | sa31 2lh | sa312lh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4438 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 242260 | 219284 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2LJ | SA312LJ | sa31 2lj | sa312lj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4637 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241727 | 219064 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2LL | SA312LL | sa31 2ll | sa312ll | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5024 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241961 | 218678 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2LN | SA312LN | sa31 2ln | sa312ln | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4539 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241726 | 219162 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2LQ | SA312LQ | sa31 2lq | sa312lq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4401 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 242158 | 219312 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NE | SA312NE | sa31 2ne | sa312ne | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4259 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 242167 | 219456 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NF | SA312NF | sa31 2nf | sa312nf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5047 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241272 | 218683 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NG | SA312NG | sa31 2ng | sa312ng | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4837 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 240908 | 218950 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NL | SA312NL | sa31 2nl | sa312nl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4176 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 242109 | 219534 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NN | SA312NN | sa31 2nn | sa312nn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4234 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241620 | 219471 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NP | SA312NP | sa31 2np | sa312np | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4251 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241965 | 219452 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NR | SA312NR | sa31 2nr | sa312nr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4025 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241997 | 219679 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NS | SA312NS | sa31 2ns | sa312ns | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3996 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 242055 | 219711 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NT | SA312NT | sa31 2nt | sa312nt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4611 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241609 | 219094 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NU | SA312NU | sa31 2nu | sa312nu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4162 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241899 | 219539 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NW | SA312NW | sa31 2nw | sa312nw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4057 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 241794 | 219643 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NX | SA312NX | sa31 2nx | sa312nx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4587 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241648 | 219117 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NY | SA312NY | sa31 2ny | sa312ny | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4114 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 242153 | 219600 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2NZ | SA312NZ | sa31 2nz | sa312nz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4123 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 242009 | 219582 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2PA | SA312PA | sa31 2pa | sa312pa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4107 | 1374 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.61 | 13.66 | 15.1 | 242241 | 219615 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2PB | SA312PB | sa31 2pb | sa312pb | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 4185 | 1392 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.94 | 13.84 | 15.29 | 242620 | 219541 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2PD | SA312PD | sa31 2pd | sa312pd | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 4104 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 242790 | 219411 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2PE | SA312PE | sa31 2pe | sa312pe | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4278 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241638 | 219426 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2PF | SA312PF | sa31 2pf | sa312pf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2PG | SA312PG | sa31 2pg | sa312pg | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 4030 | 1405 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.19 | 13.97 | 15.44 | 243213 | 218957 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2PJ | SA312PJ | sa31 2pj | sa312pj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4713 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241752 | 218988 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2PL | SA312PL | sa31 2pl | sa312pl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4647 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 241875 | 219054 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2PN | SA312PN | sa31 2pn | sa312pn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2251 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 243089 | 221841 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2PP | SA312PP | sa31 2pp | sa312pp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1946 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 243030 | 222176 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2PQ | SA312PQ | sa31 2pq | sa312pq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4582 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241473 | 219132 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2WZ | SA312WZ | sa31 2wz | sa312wz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2YB | SA312YB | sa31 2yb | sa312yb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 2ZB | SA312ZB | sa31 2zb | sa312zb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AB | SA313AB | sa31 3ab | sa313ab | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3745 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241119 | 220022 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AD | SA313AD | sa31 3ad | sa313ad | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3696 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241071 | 220081 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AE | SA313AE | sa31 3ae | sa313ae | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3743 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241034 | 220041 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AF | SA313AF | sa31 3af | sa313af | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4886 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 239318 | 219504 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AJ | SA313AJ | sa31 3aj | sa313aj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3710 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240977 | 220087 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AL | SA313AL | sa31 3al | sa313al | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3748 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240839 | 220083 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AN | SA313AN | sa31 3an | sa313an | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3796 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240990 | 219996 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AP | SA313AP | sa31 3ap | sa313ap | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3767 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240890 | 220050 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AQ | SA313AQ | sa31 3aq | sa313aq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3709 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240990 | 220085 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AR | SA313AR | sa31 3ar | sa313ar | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4049 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240718 | 219804 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AS | SA313AS | sa31 3as | sa313as | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4299 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240498 | 219610 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AX | SA313AX | sa31 3ax | sa313ax | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3902 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240760 | 219945 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AY | SA313AY | sa31 3ay | sa313ay | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3826 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240672 | 220051 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3AZ | SA313AZ | sa31 3az | sa313az | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3819 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240642 | 220068 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BA | SA313BA | sa31 3ba | sa313ba | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3814 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240601 | 220086 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BB | SA313BB | sa31 3bb | sa313bb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4469 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 239091 | 220161 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BD | SA313BD | sa31 3bd | sa313bd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3797 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240815 | 220039 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BE | SA313BE | sa31 3be | sa313be | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3813 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240834 | 220017 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BG | SA313BG | sa31 3bg | sa313bg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3782 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240835 | 220049 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BH | SA313BH | sa31 3bh | sa313bh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4159 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240651 | 219709 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BJ | SA313BJ | sa31 3bj | sa313bj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4165 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 239345 | 220351 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BL | SA313BL | sa31 3bl | sa313bl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4042 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 239420 | 220448 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BN | SA313BN | sa31 3bn | sa313bn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3767 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241071 | 220009 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BP | SA313BP | sa31 3bp | sa313bp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4866 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240072 | 219159 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BQ | SA313BQ | sa31 3bq | sa313bq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3779 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240844 | 220050 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BR | SA313BR | sa31 3br | sa313br | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5359 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 238596 | 219420 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BS | SA313BS | sa31 3bs | sa313bs | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3981 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240356 | 219998 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BT | SA313BT | sa31 3bt | sa313bt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4019 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240463 | 219917 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BU | SA313BU | sa31 3bu | sa313bu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4051 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240241 | 219970 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BW | SA313BW | sa31 3bw | sa313bw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5355 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 238528 | 219477 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BX | SA313BX | sa31 3bx | sa313bx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3946 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240414 | 220013 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BY | SA313BY | sa31 3by | sa313by | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3921 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240335 | 220071 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3BZ | SA313BZ | sa31 3bz | sa313bz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3831 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240262 | 220201 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DA | SA313DA | sa31 3da | sa313da | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5173 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 238814 | 219491 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DB | SA313DB | sa31 3db | sa313db | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4003 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240154 | 220060 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DD | SA313DD | sa31 3dd | sa313dd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3905 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240156 | 220168 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DE | SA313DE | sa31 3de | sa313de | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3889 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240385 | 220086 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DF | SA313DF | sa31 3df | sa313df | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3865 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240554 | 220049 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DG | SA313DG | sa31 3dg | sa313dg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3878 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240577 | 220027 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DH | SA313DH | sa31 3dh | sa313dh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3941 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240208 | 220104 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DJ | SA313DJ | sa31 3dj | sa313dj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3746 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240434 | 220220 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DL | SA313DL | sa31 3dl | sa313dl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3737 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240473 | 220215 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DN | SA313DN | sa31 3dn | sa313dn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3670 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240516 | 220270 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DP | SA313DP | sa31 3dp | sa313dp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3717 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240659 | 220169 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DQ | SA313DQ | sa31 3dq | sa313dq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3878 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240452 | 220072 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DR | SA313DR | sa31 3dr | sa313dr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3643 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240597 | 220269 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DS | SA313DS | sa31 3ds | sa313ds | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3589 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240626 | 220316 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DT | SA313DT | sa31 3dt | sa313dt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3536 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240593 | 220384 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DU | SA313DU | sa31 3du | sa313du | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3741 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240722 | 220124 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DW | SA313DW | sa31 3dw | sa313dw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3725 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240627 | 220172 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DX | SA313DX | sa31 3dx | sa313dx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3671 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240724 | 220197 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DY | SA313DY | sa31 3dy | sa313dy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3671 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240815 | 220170 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3DZ | SA313DZ | sa31 3dz | sa313dz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3715 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240825 | 220121 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EA | SA313EA | sa31 3ea | sa313ea | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4127 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 239287 | 220442 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EB | SA313EB | sa31 3eb | sa313eb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3668 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240853 | 220162 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3ED | SA313ED | sa31 3ed | sa313ed | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3732 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240001 | 220442 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EE | SA313EE | sa31 3ee | sa313ee | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3579 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240538 | 220359 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EF | SA313EF | sa31 3ef | sa313ef | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3597 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240376 | 220406 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EG | SA313EG | sa31 3eg | sa313eg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3740 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240125 | 220366 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EH | SA313EH | sa31 3eh | sa313eh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3724 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240309 | 220297 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EJ | SA313EJ | sa31 3ej | sa313ej | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3675 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240128 | 220438 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EL | SA313EL | sa31 3el | sa313el | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3582 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240752 | 220281 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EN | SA313EN | sa31 3en | sa313en | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4006 | 1450 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.03 | 14.41 | 15.93 | 239278 | 220604 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EP | SA313EP | sa31 3ep | sa313ep | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3976 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239731 | 220317 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EQ | SA313EQ | sa31 3eq | sa313eq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3808 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239816 | 220462 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3ER | SA313ER | sa31 3er | sa313er | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3956 | 1450 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.03 | 14.41 | 15.93 | 239464 | 220522 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3ES | SA313ES | sa31 3es | sa313es | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3883 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 239515 | 220576 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3ET | SA313ET | sa31 3et | sa313et | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4032 | 1450 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.03 | 14.41 | 15.93 | 239282 | 220567 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EU | SA313EU | sa31 3eu | sa313eu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3555 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240660 | 220340 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EW | SA313EW | sa31 3ew | sa313ew | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3647 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240757 | 220212 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EX | SA313EX | sa31 3ex | sa313ex | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3962 | 1450 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.03 | 14.41 | 15.93 | 239349 | 220604 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EY | SA313EY | sa31 3ey | sa313ey | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3902 | 1450 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.03 | 14.41 | 15.93 | 239375 | 220659 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3EZ | SA313EZ | sa31 3ez | sa313ez | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4424 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239781 | 219774 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3FA | SA313FA | sa31 3fa | sa313fa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5199 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 238782 | 219482 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3FB | SA313FB | sa31 3fb | sa313fb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5279 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 238677 | 219459 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3FD | SA313FD | sa31 3fd | sa313fd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5219 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 238699 | 219517 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3FE | SA313FE | sa31 3fe | sa313fe | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4271 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239895 | 219888 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3FF | SA313FF | sa31 3ff | sa313ff | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3937 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240810 | 219895 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3GA | SA313GA | sa31 3ga | sa313ga | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5111 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 239071 | 219392 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3GB | SA313GB | sa31 3gb | sa313gb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3557 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240246 | 220511 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3GH | SA313GH | sa31 3gh | sa313gh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3573 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240057 | 220593 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3GL | SA313GL | sa31 3gl | sa313gl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3492 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240182 | 220616 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3GR | SA313GR | sa31 3gr | sa313gr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3559 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240160 | 220552 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3GU | SA313GU | sa31 3gu | sa313gu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3466 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240190 | 220641 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HA | SA313HA | sa31 3ha | sa313ha | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4008 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239543 | 220402 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HB | SA313HB | sa31 3hb | sa313hb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4316 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 239399 | 220127 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HD | SA313HD | sa31 3hd | sa313hd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5006 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 239067 | 219519 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HE | SA313HE | sa31 3he | sa313he | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4379 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239599 | 219927 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HF | SA313HF | sa31 3hf | sa313hf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4406 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239637 | 219873 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HG | SA313HG | sa31 3hg | sa313hg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4325 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239869 | 219841 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HH | SA313HH | sa31 3hh | sa313hh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4405 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239868 | 219752 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HJ | SA313HJ | sa31 3hj | sa313hj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4447 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239866 | 219706 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HL | SA313HL | sa31 3hl | sa313hl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4498 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239803 | 219680 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HN | SA313HN | sa31 3hn | sa313hn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4822 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 239282 | 219601 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HP | SA313HP | sa31 3hp | sa313hp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4875 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 239420 | 219457 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HQ | SA313HQ | sa31 3hq | sa313hq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4297 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239782 | 219917 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HR | SA313HR | sa31 3hr | sa313hr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4777 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239590 | 219476 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HS | SA313HS | sa31 3hs | sa313hs | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4728 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239676 | 219487 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HT | SA313HT | sa31 3ht | sa313ht | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4640 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239749 | 219548 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HU | SA313HU | sa31 3hu | sa313hu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4579 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239838 | 219573 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HW | SA313HW | sa31 3hw | sa313hw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4792 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 239474 | 219522 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HX | SA313HX | sa31 3hx | sa313hx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4519 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239641 | 219742 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HY | SA313HY | sa31 3hy | sa313hy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4117 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239774 | 220128 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3HZ | SA313HZ | sa31 3hz | sa313hz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5111 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 239420 | 219188 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JA | SA313JA | sa31 3ja | sa313ja | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4689 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239616 | 219562 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JB | SA313JB | sa31 3jb | sa313jb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4562 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239917 | 219554 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JD | SA313JD | sa31 3jd | sa313jd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3560 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240741 | 220308 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JE | SA313JE | sa31 3je | sa313je | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3568 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240699 | 220313 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JF | SA313JF | sa31 3jf | sa313jf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4603 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239661 | 219635 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JG | SA313JG | sa31 3jg | sa313jg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3518 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240414 | 220476 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JH | SA313JH | sa31 3jh | sa313jh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3512 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 240502 | 220445 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JJ | SA313JJ | sa31 3jj | sa313jj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3489 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240397 | 220515 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JL | SA313JL | sa31 3jl | sa313jl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4153 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239779 | 220084 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JN | SA313JN | sa31 3jn | sa313jn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4124 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239869 | 220067 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JP | SA313JP | sa31 3jp | sa313jp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3893 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241153 | 219865 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JQ | SA313JQ | sa31 3jq | sa313jq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3613 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240254 | 220444 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JR | SA313JR | sa31 3jr | sa313jr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3841 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241320 | 219892 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JS | SA313JS | sa31 3js | sa313js | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3797 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241258 | 219945 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JT | SA313JT | sa31 3jt | sa313jt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3808 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241160 | 219950 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JU | SA313JU | sa31 3ju | sa313ju | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4312 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239643 | 219978 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3JW | SA313JW | sa31 3jw | sa313jw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4215 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239815 | 219993 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3LD | SA313LD | sa31 3ld | sa313ld | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3846 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241131 | 219917 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3LE | SA313LE | sa31 3le | sa313le | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3779 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241154 | 219980 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3LL | SA313LL | sa31 3ll | sa313ll | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3888 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241042 | 219891 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3LN | SA313LN | sa31 3ln | sa313ln | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3879 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241156 | 219879 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3LP | SA313LP | sa31 3lp | sa313lp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4124 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240128 | 219939 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3LQ | SA313LQ | sa31 3lq | sa313lq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3743 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241128 | 220022 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3LS | SA313LS | sa31 3ls | sa313ls | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4200 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240031 | 219900 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3LU | SA313LU | sa31 3lu | sa313lu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4240 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240085 | 219832 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3LW | SA313LW | sa31 3lw | sa313lw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3878 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241188 | 219874 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3LX | SA313LX | sa31 3lx | sa313lx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4315 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240035 | 219772 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3LY | SA313LY | sa31 3ly | sa313ly | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4406 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239931 | 219720 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3LZ | SA313LZ | sa31 3lz | sa313lz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4563 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240002 | 219515 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NA | SA313NA | sa31 3na | sa313na | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4334 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239946 | 219793 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NB | SA313NB | sa31 3nb | sa313nb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4778 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239939 | 219308 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NE | SA313NE | sa31 3ne | sa313ne | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4851 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239796 | 219292 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NF | SA313NF | sa31 3nf | sa313nf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4727 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240053 | 219316 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NG | SA313NG | sa31 3ng | sa313ng | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4666 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240014 | 219398 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NJ | SA313NJ | sa31 3nj | sa313nj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5076 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239983 | 218969 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NL | SA313NL | sa31 3nl | sa313nl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4997 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240245 | 218958 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NN | SA313NN | sa31 3nn | sa313nn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5189 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240112 | 218801 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NQ | SA313NQ | sa31 3nq | sa313nq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4931 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240137 | 219066 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NR | SA313NR | sa31 3nr | sa313nr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5013 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240047 | 219011 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NS | SA313NS | sa31 3ns | sa313ns | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5209 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239880 | 218866 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NU | SA313NU | sa31 3nu | sa313nu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5230 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240035 | 218784 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NW | SA313NW | sa31 3nw | sa313nw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5414 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240138 | 218554 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NX | SA313NX | sa31 3nx | sa313nx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5235 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239889 | 218835 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NY | SA313NY | sa31 3ny | sa313ny | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5303 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239901 | 218757 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3NZ | SA313NZ | sa31 3nz | sa313nz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5348 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239829 | 218737 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PA | SA313PA | sa31 3pa | sa313pa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5306 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240002 | 218716 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PB | SA313PB | sa31 3pb | sa313pb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5304 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239928 | 218745 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PD | SA313PD | sa31 3pd | sa313pd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5376 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239931 | 218667 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PE | SA313PE | sa31 3pe | sa313pe | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5427 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239954 | 218604 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PG | SA313PG | sa31 3pg | sa313pg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5381 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240057 | 218617 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PH | SA313PH | sa31 3ph | sa313ph | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5175 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239870 | 218907 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PJ | SA313PJ | sa31 3pj | sa313pj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5120 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239880 | 218962 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PL | SA313PL | sa31 3pl | sa313pl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5075 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239918 | 218995 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PN | SA313PN | sa31 3pn | sa313pn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5089 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240040 | 218933 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PP | SA313PP | sa31 3pp | sa313pp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4017 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240082 | 220079 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PQ | SA313PQ | sa31 3pq | sa313pq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5455 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 240010 | 218555 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PR | SA313PR | sa31 3pr | sa313pr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4077 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239989 | 220058 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PS | SA313PS | sa31 3ps | sa313ps | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4112 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240057 | 219985 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PT | SA313PT | sa31 3pt | sa313pt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4152 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239954 | 219991 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PU | SA313PU | sa31 3pu | sa313pu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5191 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239875 | 218888 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PW | SA313PW | sa31 3pw | sa313pw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4988 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239967 | 219069 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PX | SA313PX | sa31 3px | sa313px | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4264 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239944 | 219871 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PY | SA313PY | sa31 3py | sa313py | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4211 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239881 | 219962 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3PZ | SA313PZ | sa31 3pz | sa313pz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4071 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239926 | 220097 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QA | SA313QA | sa31 3qa | sa313qa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3152 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240203 | 220995 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QD | SA313QD | sa31 3qd | sa313qd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4265 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 239858 | 219914 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QE | SA313QE | sa31 3qe | sa313qe | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3861 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240036 | 220276 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QF | SA313QF | sa31 3qf | sa313qf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3903 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240030 | 220232 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QG | SA313QG | sa31 3qg | sa313qg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3963 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 240025 | 220167 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QL | SA313QL | sa31 3ql | sa313ql | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3021 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 240079 | 221231 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QN | SA313QN | sa31 3qn | sa313qn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2735 | 1492 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.81 | 14.83 | 16.39 | 240038 | 221625 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QP | SA313QP | sa31 3qp | sa313qp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2689 | 1492 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.81 | 14.83 | 16.39 | 239819 | 221904 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QQ | SA313QQ | sa31 3qq | sa313qq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5488 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 239132 | 218916 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QR | SA313QR | sa31 3qr | sa313qr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5493 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239792 | 218596 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QS | SA313QS | sa31 3qs | sa313qs | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4164 | 1450 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.03 | 14.41 | 15.93 | 238697 | 220947 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QT | SA313QT | sa31 3qt | sa313qt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2682 | 1492 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.81 | 14.83 | 16.39 | 239698 | 222060 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QW | SA313QW | sa31 3qw | sa313qw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3159 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 239313 | 221779 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QX | SA313QX | sa31 3qx | sa313qx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5047 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239605 | 219165 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QY | SA313QY | sa31 3qy | sa313qy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5723 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 239033 | 218702 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3QZ | SA313QZ | sa31 3qz | sa313qz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5128 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239700 | 219031 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3RB | SA313RB | sa31 3rb | sa313rb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5238 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 239209 | 219160 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3RD | SA313RD | sa31 3rd | sa313rd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4952 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239606 | 219271 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3RG | SA313RG | sa31 3rg | sa313rg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3761 | 1443 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.9 | 14.34 | 15.85 | 239710 | 220587 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3RJ | SA313RJ | sa31 3rj | sa313rj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5695 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 238610 | 218996 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3RL | SA313RL | sa31 3rl | sa313rl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5739 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 238577 | 218966 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3RN | SA313RN | sa31 3rn | sa313rn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5850 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 238593 | 218821 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3RP | SA313RP | sa31 3rp | sa313rp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5603 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 238223 | 219405 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3RR | SA313RR | sa31 3rr | sa313rr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5468 | 1395 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26 | 13.87 | 15.33 | 237695 | 220111 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3RS | SA313RS | sa31 3rs | sa313rs | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5681 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 238314 | 219231 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3RU | SA313RU | sa31 3ru | sa313ru | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5175 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 239299 | 219181 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3RY | SA313RY | sa31 3ry | sa313ry | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5037 | 1370 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.53 | 13.62 | 15.05 | 239504 | 219228 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3SA | SA313SA | sa31 3sa | sa313sa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5747 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 238413 | 219072 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3SB | SA313SB | sa31 3sb | sa313sb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5099 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 238921 | 219506 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3SD | SA313SD | sa31 3sd | sa313sd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5155 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 238859 | 219481 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3SE | SA313SE | sa31 3se | sa313se | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5157 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 238916 | 219439 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3SG | SA313SG | sa31 3sg | sa313sg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5490 | 1395 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26 | 13.87 | 15.33 | 238248 | 219532 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 3ZB | SA313ZB | sa31 3zb | sa313zb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9BF | SA319BF | sa31 9bf | sa319bf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9BP | SA319BP | sa31 9bp | sa319bp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9BU | SA319BU | sa31 9bu | sa319bu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9BW | SA319BW | sa31 9bw | sa319bw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9BY | SA319BY | sa31 9by | sa319by | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9BZ | SA319BZ | sa31 9bz | sa319bz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9DA | SA319DA | sa31 9da | sa319da | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9DH | SA319DH | sa31 9dh | sa319dh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9DL | SA319DL | sa31 9dl | sa319dl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9DN | SA319DN | sa31 9dn | sa319dn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9DP | SA319DP | sa31 9dp | sa319dp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9DQ | SA319DQ | sa31 9dq | sa319dq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9DR | SA319DR | sa31 9dr | sa319dr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9ED | SA319ED | sa31 9ed | sa319ed | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9EL | SA319EL | sa31 9el | sa319el | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9ER | SA319ER | sa31 9er | sa319er | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9ET | SA319ET | sa31 9et | sa319et | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9EX | SA319EX | sa31 9ex | sa319ex | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9FE | SA319FE | sa31 9fe | sa319fe | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9FG | SA319FG | sa31 9fg | sa319fg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9SA | SA319SA | sa31 9sa | sa319sa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3725 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241407 | 219998 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9SB | SA319SB | sa31 9sb | sa319sb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3725 | 1355 | 1200to1500 | 2.71 | 1.98 | 1.46 | 25.26 | 13.47 | 14.89 | 241407 | 219998 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA31 9ZZ | SA319ZZ | sa31 9zz | sa319zz | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241298 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AA | SA327AA | sa32 7aa | sa327aa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2186 | 1492 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.81 | 14.83 | 16.39 | 243951 | 223212 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AB | SA327AB | sa32 7ab | sa327ab | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2013 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 243793 | 224100 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AD | SA327AD | sa32 7ad | sa327ad | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2708 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 244697 | 223767 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AE | SA327AE | sa32 7ae | sa327ae | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1632 | 1538 | Over1500 | 3.08 | 2.25 | 1.65 | 28.67 | 15.29 | 16.9 | 245252 | 222837 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AF | SA327AF | sa32 7af | sa327af | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2601 | 1556 | Over1500 | 3.11 | 2.28 | 1.67 | 29 | 15.47 | 17.1 | 245667 | 224097 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AG | SA327AG | sa32 7ag | sa327ag | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2918 | 1537 | Over1500 | 3.08 | 2.25 | 1.65 | 28.65 | 15.28 | 16.89 | 244639 | 224453 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AH | SA327AH | sa32 7ah | sa327ah | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3271 | 1606 | Over1500 | 3.21 | 2.35 | 1.72 | 29.93 | 15.96 | 17.64 | 244278 | 225857 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AJ | SA327AJ | sa32 7aj | sa327aj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3656 | 1702 | Over1500 | 3.41 | 2.49 | 1.83 | 31.72 | 16.92 | 18.7 | 244777 | 225850 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AL | SA327AL | sa32 7al | sa327al | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4213 | 1702 | Over1500 | 3.41 | 2.49 | 1.83 | 31.72 | 16.92 | 18.7 | 245345 | 226007 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AN | SA327AN | sa32 7an | sa327an | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 4415 | 1733 | Over1500 | 3.47 | 2.54 | 1.86 | 32.3 | 17.23 | 19.04 | 245831 | 225962 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AP | SA327AP | sa32 7ap | sa327ap | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 4167 | 1706 | Over1500 | 3.41 | 2.5 | 1.83 | 31.8 | 16.96 | 18.74 | 244985 | 226796 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AQ | SA327AQ | sa32 7aq | sa327aq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2899 | 1591 | Over1500 | 3.18 | 2.33 | 1.71 | 29.65 | 15.82 | 17.48 | 244406 | 225010 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AR | SA327AR | sa32 7ar | sa327ar | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2774 | 1606 | Over1500 | 3.21 | 2.35 | 1.72 | 29.93 | 15.96 | 17.64 | 243859 | 225581 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AS | SA327AS | sa32 7as | sa327as | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1983 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 243771 | 224053 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AT | SA327AT | sa32 7at | sa327at | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1977 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 243760 | 224080 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AU | SA327AU | sa32 7au | sa327au | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2026 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 243822 | 224010 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AW | SA327AW | sa32 7aw | sa327aw | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 657 | 1700 | Over1500 | 3.4 | 2.49 | 1.83 | 31.69 | 16.9 | 18.68 | 244661 | 231849 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AX | SA327AX | sa32 7ax | sa327ax | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1975 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 243776 | 223974 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AY | SA327AY | sa32 7ay | sa327ay | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1644 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 247917 | 221719 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7AZ | SA327AZ | sa32 7az | sa327az | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 3248 | 1622 | Over1500 | 3.25 | 2.38 | 1.74 | 30.23 | 16.12 | 17.82 | 244069 | 227102 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BA | SA327BA | sa32 7ba | sa327ba | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 578 | 1574 | Over1500 | 3.15 | 2.31 | 1.69 | 29.34 | 15.65 | 17.29 | 250681 | 223852 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BB | SA327BB | sa32 7bb | sa327bb | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1728 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 251089 | 226113 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BD | SA327BD | sa32 7bd | sa327bd | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 2355 | 1849 | Over1500 | 3.7 | 2.71 | 1.99 | 34.46 | 18.38 | 20.31 | 251138 | 228775 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BE | SA327BE | sa32 7be | sa327be | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 1347 | 1793 | Over1500 | 3.59 | 2.63 | 1.93 | 33.42 | 17.82 | 19.7 | 251765 | 229747 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BH | SA327BH | sa32 7bh | sa327bh | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 966 | 1658 | Over1500 | 3.32 | 2.43 | 1.78 | 30.9 | 16.48 | 18.22 | 256214 | 232650 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BJ | SA327BJ | sa32 7bj | sa327bj | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 839 | 1643 | Over1500 | 3.29 | 2.41 | 1.76 | 30.62 | 16.33 | 18.05 | 257858 | 233584 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BL | SA327BL | sa32 7bl | sa327bl | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 947 | 1731 | Over1500 | 3.46 | 2.54 | 1.86 | 32.26 | 17.21 | 19.02 | 252233 | 230628 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BN | SA327BN | sa32 7bn | sa327bn | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 1581 | 1731 | Over1500 | 3.46 | 2.54 | 1.86 | 32.26 | 17.21 | 19.02 | 251841 | 231168 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BP | SA327BP | sa32 7bp | sa327bp | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 3463 | 1754 | Over1500 | 3.51 | 2.57 | 1.88 | 32.69 | 17.44 | 19.27 | 251839 | 233394 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BQ | SA327BQ | sa32 7bq | sa327bq | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 628 | 1795 | Over1500 | 3.59 | 2.63 | 1.93 | 33.46 | 17.84 | 19.72 | 256073 | 232258 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BR | SA327BR | sa32 7br | sa327br | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 3995 | 1592 | Over1500 | 3.19 | 2.33 | 1.71 | 29.67 | 15.83 | 17.49 | 255837 | 227289 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BS | SA327BS | sa32 7bs | sa327bs | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 4784 | 1751 | Over1500 | 3.5 | 2.56 | 1.88 | 32.64 | 17.41 | 19.24 | 251601 | 234771 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BT | SA327BT | sa32 7bt | sa327bt | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1806 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 243589 | 224065 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BU | SA327BU | sa32 7bu | sa327bu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1906 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 243690 | 224067 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BW | SA327BW | sa32 7bw | sa327bw | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 1975 | 1771 | Over1500 | 3.54 | 2.59 | 1.9 | 33.01 | 17.6 | 19.46 | 252375 | 232006 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BX | SA327BX | sa32 7bx | sa327bx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1895 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 243689 | 224013 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BY | SA327BY | sa32 7by | sa327by | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 3025 | 1573 | Over1500 | 3.15 | 2.3 | 1.69 | 29.32 | 15.64 | 17.28 | 255246 | 225697 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7BZ | SA327BZ | sa32 7bz | sa327bz | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 3207 | 1573 | Over1500 | 3.15 | 2.3 | 1.69 | 29.32 | 15.64 | 17.28 | 254703 | 225764 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DA | SA327DA | sa32 7da | sa327da | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 3822 | 1592 | Over1500 | 3.19 | 2.33 | 1.71 | 29.67 | 15.83 | 17.49 | 255531 | 226520 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DB | SA327DB | sa32 7db | sa327db | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 3796 | 1554 | Over1500 | 3.11 | 2.28 | 1.67 | 28.96 | 15.45 | 17.07 | 256118 | 226466 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DD | SA327DD | sa32 7dd | sa327dd | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 4544 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 257061 | 227019 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DE | SA327DE | sa32 7de | sa327de | Carmarthenshire | Sir Gaerfyrddin | Salem STW | 4385 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 257844 | 227610 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DH | SA327DH | sa32 7dh | sa327dh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2125 | 1417 | 1200to1500 | 2.84 | 2.08 | 1.52 | 26.41 | 14.09 | 15.57 | 243348 | 222224 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DJ | SA327DJ | sa32 7dj | sa327dj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1668 | 1535 | Over1500 | 3.07 | 2.25 | 1.65 | 28.61 | 15.26 | 16.86 | 243482 | 223839 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DL | SA327DL | sa32 7dl | sa327dl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1817 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 243536 | 224296 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DN | SA327DN | sa32 7dn | sa327dn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1802 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 243544 | 224223 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DP | SA327DP | sa32 7dp | sa327dp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2293 | 1591 | Over1500 | 3.18 | 2.33 | 1.71 | 29.65 | 15.82 | 17.48 | 243764 | 224916 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DQ | SA327DQ | sa32 7dq | sa327dq | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 3333 | 1622 | Over1500 | 3.25 | 2.38 | 1.74 | 30.23 | 16.12 | 17.82 | 244151 | 227069 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DR | SA327DR | sa32 7dr | sa327dr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3178 | 1606 | Over1500 | 3.21 | 2.35 | 1.72 | 29.93 | 15.96 | 17.64 | 243810 | 226178 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DS | SA327DS | sa32 7ds | sa327ds | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 3306 | 1622 | Over1500 | 3.25 | 2.38 | 1.74 | 30.23 | 16.12 | 17.82 | 244033 | 226969 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DT | SA327DT | sa32 7dt | sa327dt | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 3156 | 1622 | Over1500 | 3.25 | 2.38 | 1.74 | 30.23 | 16.12 | 17.82 | 244110 | 227308 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DU | SA327DU | sa32 7du | sa327du | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 2765 | 1607 | Over1500 | 3.22 | 2.35 | 1.73 | 29.95 | 15.97 | 17.66 | 244224 | 228478 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DW | SA327DW | sa32 7dw | sa327dw | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 3241 | 1622 | Over1500 | 3.25 | 2.38 | 1.74 | 30.23 | 16.12 | 17.82 | 243982 | 227010 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DX | SA327DX | sa32 7dx | sa327dx | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 1668 | 1639 | Over1500 | 3.28 | 2.4 | 1.76 | 30.55 | 16.29 | 18.01 | 244119 | 229642 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DY | SA327DY | sa32 7dy | sa327dy | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 1570 | 1633 | Over1500 | 3.27 | 2.39 | 1.75 | 30.44 | 16.23 | 17.94 | 244804 | 229813 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7DZ | SA327DZ | sa32 7dz | sa327dz | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 1006 | 1639 | Over1500 | 3.28 | 2.4 | 1.76 | 30.55 | 16.29 | 18.01 | 244313 | 230294 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7EA | SA327EA | sa32 7ea | sa327ea | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 670 | 1700 | Over1500 | 3.4 | 2.49 | 1.83 | 31.69 | 16.9 | 18.68 | 244929 | 231530 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7EB | SA327EB | sa32 7eb | sa327eb | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 539 | 1700 | Over1500 | 3.4 | 2.49 | 1.83 | 31.69 | 16.9 | 18.68 | 244542 | 231782 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7ED | SA327ED | sa32 7ed | sa327ed | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 1970 | 1751 | Over1500 | 3.5 | 2.56 | 1.88 | 32.64 | 17.41 | 19.24 | 245600 | 232780 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7EE | SA327EE | sa32 7ee | sa327ee | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 1506 | 1703 | Over1500 | 3.41 | 2.49 | 1.83 | 31.74 | 16.93 | 18.71 | 244514 | 232791 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7EG | SA327EG | sa32 7eg | sa327eg | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 1489 | 1758 | Over1500 | 3.52 | 2.57 | 1.89 | 32.77 | 17.48 | 19.31 | 243564 | 232594 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7EJ | SA327EJ | sa32 7ej | sa327ej | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1441 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 244873 | 221261 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7EL | SA327EL | sa32 7el | sa327el | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 48 | 1448 | 1200to1500 | 2.9 | 2.12 | 1.56 | 26.99 | 14.39 | 15.91 | 246234 | 221582 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7EN | SA327EN | sa32 7en | sa327en | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 143 | 1398 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.06 | 13.9 | 15.36 | 246365 | 221455 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7EP | SA327EP | sa32 7ep | sa327ep | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 918 | 1398 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.06 | 13.9 | 15.36 | 245501 | 221085 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7ER | SA327ER | sa32 7er | sa327er | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1319 | 1501 | Over1500 | 3 | 2.2 | 1.61 | 27.98 | 14.92 | 16.49 | 244962 | 221537 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7ES | SA327ES | sa32 7es | sa327es | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1239 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 246358 | 222806 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7ET | SA327ET | sa32 7et | sa327et | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 706 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 246557 | 222219 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7EU | SA327EU | sa32 7eu | sa327eu | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1197 | 1503 | Over1500 | 3.01 | 2.2 | 1.61 | 28.01 | 14.94 | 16.51 | 246997 | 222528 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7EW | SA327EW | sa32 7ew | sa327ew | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 666 | 1394 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.98 | 13.86 | 15.32 | 246870 | 221879 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7EX | SA327EX | sa32 7ex | sa327ex | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2557 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 248388 | 223017 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7EY | SA327EY | sa32 7ey | sa327ey | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1876 | 1444 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.91 | 14.35 | 15.87 | 248113 | 221970 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HA | SA327HA | sa32 7ha | sa327ha | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1850 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 249023 | 224277 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HB | SA327HB | sa32 7hb | sa327hb | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1987 | 1503 | Over1500 | 3.01 | 2.2 | 1.61 | 28.01 | 14.94 | 16.51 | 247220 | 223320 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HD | SA327HD | sa32 7hd | sa327hd | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 2440 | 1637 | Over1500 | 3.28 | 2.4 | 1.76 | 30.51 | 16.27 | 17.99 | 248449 | 224711 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HE | SA327HE | sa32 7he | sa327he | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 2585 | 1637 | Over1500 | 3.28 | 2.4 | 1.76 | 30.51 | 16.27 | 17.99 | 248402 | 225169 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HF | SA327HF | sa32 7hf | sa327hf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1712 | 1535 | Over1500 | 3.07 | 2.25 | 1.65 | 28.61 | 15.26 | 16.86 | 243483 | 224108 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HG | SA327HG | sa32 7hg | sa327hg | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 3205 | 1637 | Over1500 | 3.28 | 2.4 | 1.76 | 30.51 | 16.27 | 17.99 | 247771 | 225219 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HH | SA327HH | sa32 7hh | sa327hh | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 3968 | 1755 | Over1500 | 3.51 | 2.57 | 1.88 | 32.71 | 17.45 | 19.28 | 247142 | 225758 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HJ | SA327HJ | sa32 7hj | sa327hj | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 3201 | 1679 | Over1500 | 3.36 | 2.46 | 1.8 | 31.29 | 16.69 | 18.45 | 246697 | 224743 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HL | SA327HL | sa32 7hl | sa327hl | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1626 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 246140 | 223190 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HN | SA327HN | sa32 7hn | sa327hn | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2019 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 243767 | 224235 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HQ | SA327HQ | sa32 7hq | sa327hq | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 3616 | 1754 | Over1500 | 3.51 | 2.57 | 1.88 | 32.69 | 17.44 | 19.27 | 247695 | 226131 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HR | SA327HR | sa32 7hr | sa327hr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1275 | 1466 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.32 | 14.57 | 16.11 | 242838 | 222933 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HS | SA327HS | sa32 7hs | sa327hs | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1516 | 1535 | Over1500 | 3.07 | 2.25 | 1.65 | 28.61 | 15.26 | 16.86 | 243299 | 224034 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HT | SA327HT | sa32 7ht | sa327ht | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1798 | 1535 | Over1500 | 3.07 | 2.25 | 1.65 | 28.61 | 15.26 | 16.86 | 243443 | 224473 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HU | SA327HU | sa32 7hu | sa327hu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 998 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 242332 | 224556 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HW | SA327HW | sa32 7hw | sa327hw | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1885 | 1546 | Over1500 | 3.09 | 2.26 | 1.66 | 28.82 | 15.37 | 16.99 | 243629 | 224230 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HX | SA327HX | sa32 7hx | sa327hx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2439 | 1580 | Over1500 | 3.16 | 2.31 | 1.7 | 29.45 | 15.71 | 17.36 | 243302 | 225637 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7HY | SA327HY | sa32 7hy | sa327hy | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 3492 | 1706 | Over1500 | 3.41 | 2.5 | 1.83 | 31.8 | 16.96 | 18.74 | 244620 | 227496 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JA | SA327JA | sa32 7ja | sa327ja | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 3393 | 1671 | Over1500 | 3.34 | 2.45 | 1.79 | 31.14 | 16.61 | 18.36 | 245475 | 228117 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JB | SA327JB | sa32 7jb | sa327jb | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 2150 | 1603 | Over1500 | 3.21 | 2.35 | 1.72 | 29.88 | 15.93 | 17.61 | 244562 | 229166 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JD | SA327JD | sa32 7jd | sa327jd | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 2884 | 1700 | Over1500 | 3.4 | 2.49 | 1.83 | 31.69 | 16.9 | 18.68 | 246801 | 229865 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JE | SA327JE | sa32 7je | sa327je | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 2775 | 1671 | Over1500 | 3.34 | 2.45 | 1.79 | 31.14 | 16.61 | 18.36 | 246146 | 229229 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JF | SA327JF | sa32 7jf | sa327jf | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 3753 | 1780 | Over1500 | 3.56 | 2.61 | 1.91 | 33.18 | 17.69 | 19.56 | 247611 | 229534 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JG | SA327JG | sa32 7jg | sa327jg | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 4097 | 1776 | Over1500 | 3.55 | 2.6 | 1.91 | 33.1 | 17.65 | 19.51 | 247595 | 228866 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JH | SA327JH | sa32 7jh | sa327jh | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 4053 | 1770 | Over1500 | 3.54 | 2.59 | 1.9 | 32.99 | 17.59 | 19.45 | 246979 | 228259 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JJ | SA327JJ | sa32 7jj | sa327jj | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 3671 | 1813 | Over1500 | 3.63 | 2.66 | 1.95 | 33.79 | 18.02 | 19.92 | 248370 | 227087 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JL | SA327JL | sa32 7jl | sa327jl | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 5036 | 1743 | Over1500 | 3.49 | 2.55 | 1.87 | 32.49 | 17.33 | 19.15 | 246344 | 226608 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JQ | SA327JQ | sa32 7jq | sa327jq | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 4557 | 1861 | Over1500 | 3.72 | 2.73 | 2 | 34.69 | 18.5 | 20.45 | 248604 | 229151 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JS | SA327JS | sa32 7js | sa327js | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 2849 | 1842 | Over1500 | 3.69 | 2.7 | 1.98 | 34.33 | 18.31 | 20.24 | 251407 | 227823 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JT | SA327JT | sa32 7jt | sa327jt | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 2699 | 1842 | Over1500 | 3.69 | 2.7 | 1.98 | 34.33 | 18.31 | 20.24 | 250976 | 228423 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JU | SA327JU | sa32 7ju | sa327ju | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 3712 | 1794 | Over1500 | 3.59 | 2.63 | 1.93 | 33.44 | 17.83 | 19.71 | 249994 | 228006 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JX | SA327JX | sa32 7jx | sa327jx | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 3144 | 1821 | Over1500 | 3.64 | 2.67 | 1.96 | 33.94 | 18.1 | 20.01 | 249269 | 227105 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JY | SA327JY | sa32 7jy | sa327jy | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 2582 | 1672 | Over1500 | 3.35 | 2.45 | 1.8 | 31.16 | 16.62 | 18.37 | 252809 | 227580 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7JZ | SA327JZ | sa32 7jz | sa327jz | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 2830 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 253106 | 227321 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LA | SA327LA | sa32 7la | sa327la | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 2631 | 1744 | Over1500 | 3.49 | 2.55 | 1.87 | 32.51 | 17.34 | 19.16 | 252007 | 227735 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LE | SA327LE | sa32 7le | sa327le | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1227 | 1456 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.14 | 14.47 | 16 | 249340 | 221747 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LF | SA327LF | sa32 7lf | sa327lf | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1169 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 249279 | 221156 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LG | SA327LG | sa32 7lg | sa327lg | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1112 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 249335 | 221261 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LH | SA327LH | sa32 7lh | sa327lh | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1811 | 1426 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.58 | 14.18 | 15.67 | 249469 | 219692 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LJ | SA327LJ | sa32 7lj | sa327lj | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1632 | 1426 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.58 | 14.18 | 15.67 | 249345 | 220013 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LL | SA327LL | sa32 7ll | sa327ll | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1041 | 1501 | Over1500 | 3 | 2.2 | 1.61 | 27.98 | 14.92 | 16.49 | 250530 | 223415 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LN | SA327LN | sa32 7ln | sa327ln | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 507 | 1574 | Over1500 | 3.15 | 2.31 | 1.69 | 29.34 | 15.65 | 17.29 | 250673 | 223932 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LP | SA327LP | sa32 7lp | sa327lp | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1742 | 1513 | Over1500 | 3.03 | 2.22 | 1.62 | 28.2 | 15.04 | 16.62 | 249807 | 223019 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LQ | SA327LQ | sa32 7lq | sa327lq | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1198 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 249336 | 220766 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LR | SA327LR | sa32 7lr | sa327lr | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1898 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 249257 | 223398 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LS | SA327LS | sa32 7ls | sa327ls | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1174 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 249287 | 221402 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LT | SA327LT | sa32 7lt | sa327lt | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1226 | 1456 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.14 | 14.47 | 16 | 249310 | 221677 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LU | SA327LU | sa32 7lu | sa327lu | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1048 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 249551 | 221762 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LX | SA327LX | sa32 7lx | sa327lx | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 863 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 249754 | 221732 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LY | SA327LY | sa32 7ly | sa327ly | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 638 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 250025 | 221696 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7LZ | SA327LZ | sa32 7lz | sa327lz | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 543 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 250326 | 221747 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NA | SA327NA | sa32 7na | sa327na | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 505 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 250454 | 221722 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NB | SA327NB | sa32 7nb | sa327nb | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 750 | 1437 | 1200to1500 | 2.88 | 2.1 | 1.54 | 26.78 | 14.28 | 15.79 | 250446 | 221967 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7ND | SA327ND | sa32 7nd | sa327nd | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 329 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 250471 | 220889 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NE | SA327NE | sa32 7ne | sa327ne | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1084 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 251089 | 222089 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NF | SA327NF | sa32 7nf | sa327nf | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 723 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 250867 | 221805 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NG | SA327NG | sa32 7ng | sa327ng | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 629 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 250736 | 221775 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NH | SA327NH | sa32 7nh | sa327nh | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1001 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 251339 | 221669 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NJ | SA327NJ | sa32 7nj | sa327nj | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1487 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 251910 | 221474 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NL | SA327NL | sa32 7nl | sa327nl | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 2599 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 253425 | 221357 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NN | SA327NN | sa32 7nn | sa327nn | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1946 | 1481 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.6 | 14.72 | 16.27 | 253704 | 222702 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NP | SA327NP | sa32 7np | sa327np | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 2452 | 1489 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.75 | 14.8 | 16.36 | 252568 | 222632 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NQ | SA327NQ | sa32 7nq | sa327nq | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 575 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 250747 | 221707 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NR | SA327NR | sa32 7nr | sa327nr | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 2244 | 1474 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.47 | 14.65 | 16.19 | 252253 | 222547 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NT | SA327NT | sa32 7nt | sa327nt | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 741 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 250935 | 221773 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NU | SA327NU | sa32 7nu | sa327nu | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 878 | 1440 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.84 | 14.31 | 15.82 | 250862 | 221990 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7NY | SA327NY | sa32 7ny | sa327ny | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1507 | 1513 | Over1500 | 3.03 | 2.22 | 1.62 | 28.2 | 15.04 | 16.62 | 249730 | 222543 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PA | SA327PA | sa32 7pa | sa327pa | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1386 | 1501 | Over1500 | 3 | 2.2 | 1.61 | 27.98 | 14.92 | 16.49 | 250979 | 223018 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PB | SA327PB | sa32 7pb | sa327pb | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 626 | 1574 | Over1500 | 3.15 | 2.31 | 1.69 | 29.34 | 15.65 | 17.29 | 250989 | 223785 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PD | SA327PD | sa32 7pd | sa327pd | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1316 | 1550 | Over1500 | 3.1 | 2.27 | 1.66 | 28.89 | 15.41 | 17.03 | 252162 | 224154 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PE | SA327PE | sa32 7pe | sa327pe | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1116 | 1501 | Over1500 | 3 | 2.2 | 1.61 | 27.98 | 14.92 | 16.49 | 251447 | 223444 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PF | SA327PF | sa32 7pf | sa327pf | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1450 | 1501 | Over1500 | 3 | 2.2 | 1.61 | 27.98 | 14.92 | 16.49 | 251335 | 223026 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PG | SA327PG | sa32 7pg | sa327pg | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1975 | 1568 | Over1500 | 3.14 | 2.3 | 1.68 | 29.23 | 15.59 | 17.23 | 252833 | 224604 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PH | SA327PH | sa32 7ph | sa327ph | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 2307 | 1568 | Over1500 | 3.14 | 2.3 | 1.68 | 29.23 | 15.59 | 17.23 | 252914 | 225467 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PJ | SA327PJ | sa32 7pj | sa327pj | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 2649 | 1568 | Over1500 | 3.14 | 2.3 | 1.68 | 29.23 | 15.59 | 17.23 | 253452 | 224984 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PL | SA327PL | sa32 7pl | sa327pl | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 2390 | 1512 | Over1500 | 3.03 | 2.21 | 1.62 | 28.18 | 15.03 | 16.61 | 253841 | 224261 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PR | SA327PR | sa32 7pr | sa327pr | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 225 | 1592 | Over1500 | 3.19 | 2.33 | 1.71 | 29.67 | 15.83 | 17.49 | 250863 | 224624 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PS | SA327PS | sa32 7ps | sa327ps | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 351 | 1592 | Over1500 | 3.19 | 2.33 | 1.71 | 29.67 | 15.83 | 17.49 | 250592 | 224615 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PT | SA327PT | sa32 7pt | sa327pt | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 309 | 1592 | Over1500 | 3.19 | 2.33 | 1.71 | 29.67 | 15.83 | 17.49 | 250783 | 224696 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PU | SA327PU | sa32 7pu | sa327pu | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1485 | 1591 | Over1500 | 3.18 | 2.33 | 1.71 | 29.65 | 15.82 | 17.48 | 249645 | 225239 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PX | SA327PX | sa32 7px | sa327px | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1873 | 1668 | Over1500 | 3.34 | 2.44 | 1.79 | 31.09 | 16.58 | 18.33 | 250083 | 226099 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7PY | SA327PY | sa32 7py | sa327py | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 2852 | 1768 | Over1500 | 3.54 | 2.59 | 1.9 | 32.95 | 17.57 | 19.42 | 250768 | 227249 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QA | SA327QA | sa32 7qa | sa327qa | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 2107 | 1605 | Over1500 | 3.21 | 2.35 | 1.72 | 29.91 | 15.95 | 17.63 | 251630 | 226363 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QB | SA327QB | sa32 7qb | sa327qb | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1819 | 1605 | Over1500 | 3.21 | 2.35 | 1.72 | 29.91 | 15.95 | 17.63 | 252274 | 225554 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QD | SA327QD | sa32 7qd | sa327qd | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 875 | 1592 | Over1500 | 3.19 | 2.33 | 1.71 | 29.67 | 15.83 | 17.49 | 251371 | 225116 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QE | SA327QE | sa32 7qe | sa327qe | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1350 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 250943 | 225747 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QG | SA327QG | sa32 7qg | sa327qg | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 1939 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 250599 | 226319 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QJ | SA327QJ | sa32 7qj | sa327qj | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 754 | 1793 | Over1500 | 3.59 | 2.63 | 1.93 | 33.42 | 17.82 | 19.7 | 252451 | 229692 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QL | SA327QL | sa32 7ql | sa327ql | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 1899 | 1849 | Over1500 | 3.7 | 2.71 | 1.99 | 34.46 | 18.38 | 20.31 | 251367 | 229271 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QN | SA327QN | sa32 7qn | sa327qn | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 2378 | 1772 | Over1500 | 3.55 | 2.6 | 1.9 | 33.03 | 17.61 | 19.47 | 250731 | 229625 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QP | SA327QP | sa32 7qp | sa327qp | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 2016 | 1772 | Over1500 | 3.55 | 2.6 | 1.9 | 33.03 | 17.61 | 19.47 | 251055 | 230437 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QR | SA327QR | sa32 7qr | sa327qr | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 1690 | 1731 | Over1500 | 3.46 | 2.54 | 1.86 | 32.26 | 17.21 | 19.02 | 251542 | 230913 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QS | SA327QS | sa32 7qs | sa327qs | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 2874 | 1784 | Over1500 | 3.57 | 2.61 | 1.92 | 33.25 | 17.73 | 19.6 | 251135 | 232292 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QW | SA327QW | sa32 7qw | sa327qw | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 3115 | 1794 | Over1500 | 3.59 | 2.63 | 1.93 | 33.44 | 17.83 | 19.71 | 249936 | 230180 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QX | SA327QX | sa32 7qx | sa327qx | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 387 | 1696 | Over1500 | 3.39 | 2.48 | 1.82 | 31.61 | 16.86 | 18.63 | 252690 | 230293 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QY | SA327QY | sa32 7qy | sa327qy | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 496 | 1696 | Over1500 | 3.39 | 2.48 | 1.82 | 31.61 | 16.86 | 18.63 | 252596 | 230350 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7QZ | SA327QZ | sa32 7qz | sa327qz | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 631 | 1793 | Over1500 | 3.59 | 2.63 | 1.93 | 33.42 | 17.82 | 19.7 | 252473 | 230406 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RA | SA327RA | sa32 7ra | sa327ra | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 659 | 1793 | Over1500 | 3.59 | 2.63 | 1.93 | 33.42 | 17.82 | 19.7 | 252394 | 230211 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RB | SA327RB | sa32 7rb | sa327rb | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 321 | 1696 | Over1500 | 3.39 | 2.48 | 1.82 | 31.61 | 16.86 | 18.63 | 252916 | 230442 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RD | SA327RD | sa32 7rd | sa327rd | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 1496 | 1736 | Over1500 | 3.47 | 2.54 | 1.86 | 32.36 | 17.26 | 19.07 | 254201 | 231259 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RE | SA327RE | sa32 7re | sa327re | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 190 | 1795 | Over1500 | 3.59 | 2.63 | 1.93 | 33.46 | 17.84 | 19.72 | 255526 | 232188 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RG | SA327RG | sa32 7rg | sa327rg | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 782 | 1767 | Over1500 | 3.54 | 2.59 | 1.9 | 32.93 | 17.56 | 19.41 | 255373 | 231229 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RH | SA327RH | sa32 7rh | sa327rh | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 1645 | 1762 | Over1500 | 3.53 | 2.58 | 1.89 | 32.84 | 17.52 | 19.36 | 253314 | 231773 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RN | SA327RN | sa32 7rn | sa327rn | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 2159 | 1658 | Over1500 | 3.32 | 2.43 | 1.78 | 30.9 | 16.48 | 18.22 | 253510 | 232837 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RP | SA327RP | sa32 7rp | sa327rp | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 2591 | 1684 | Over1500 | 3.37 | 2.47 | 1.81 | 31.39 | 16.74 | 18.5 | 254490 | 234386 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RR | SA327RR | sa32 7rr | sa327rr | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 4033 | 1636 | Over1500 | 3.27 | 2.4 | 1.76 | 30.49 | 16.26 | 17.97 | 254541 | 235917 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RS | SA327RS | sa32 7rs | sa327rs | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 3257 | 1608 | Over1500 | 3.22 | 2.35 | 1.73 | 29.97 | 15.98 | 17.67 | 254582 | 237484 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RT | SA327RT | sa32 7rt | sa327rt | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 3006 | 1680 | Over1500 | 3.36 | 2.46 | 1.8 | 31.31 | 16.7 | 18.46 | 254619 | 238061 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RU | SA327RU | sa32 7ru | sa327ru | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 3475 | 1636 | Over1500 | 3.27 | 2.4 | 1.76 | 30.49 | 16.26 | 17.97 | 255085 | 236443 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RY | SA327RY | sa32 7ry | sa327ry | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 3060 | 1734 | Over1500 | 3.47 | 2.54 | 1.86 | 32.32 | 17.24 | 19.05 | 253096 | 233892 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7RZ | SA327RZ | sa32 7rz | sa327rz | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 3280 | 1734 | Over1500 | 3.47 | 2.54 | 1.86 | 32.32 | 17.24 | 19.05 | 252909 | 234011 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7SA | SA327SA | sa32 7sa | sa327sa | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 3595 | 1734 | Over1500 | 3.47 | 2.54 | 1.86 | 32.32 | 17.24 | 19.05 | 252903 | 234485 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7SB | SA327SB | sa32 7sb | sa327sb | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 3418 | 1687 | Over1500 | 3.38 | 2.47 | 1.81 | 31.44 | 16.77 | 18.53 | 253370 | 234672 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7SD | SA327SD | sa32 7sd | sa327sd | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 4755 | 1705 | Over1500 | 3.41 | 2.5 | 1.83 | 31.78 | 16.95 | 18.73 | 252650 | 235806 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7SE | SA327SE | sa32 7se | sa327se | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 4338 | 1733 | Over1500 | 3.47 | 2.54 | 1.86 | 32.3 | 17.23 | 19.04 | 252396 | 237267 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7SG | SA327SG | sa32 7sg | sa327sg | Carmarthenshire | Sir Gaerfyrddin | Bro Dolau STW | 4062 | 1676 | Over1500 | 3.35 | 2.45 | 1.8 | 31.24 | 16.66 | 18.41 | 253516 | 238111 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7SJ | SA327SJ | sa32 7sj | sa327sj | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 151 | 1649 | Over1500 | 3.3 | 2.42 | 1.77 | 30.73 | 16.39 | 18.12 | 258589 | 233663 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7SL | SA327SL | sa32 7sl | sa327sl | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 132 | 1649 | Over1500 | 3.3 | 2.42 | 1.77 | 30.73 | 16.39 | 18.12 | 258564 | 233712 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7SN | SA327SN | sa32 7sn | sa327sn | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 296 | 1643 | Over1500 | 3.29 | 2.41 | 1.76 | 30.62 | 16.33 | 18.05 | 258422 | 233630 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7SR | SA327SR | sa32 7sr | sa327sr | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 3175 | 1674 | Over1500 | 3.35 | 2.45 | 1.8 | 31.2 | 16.64 | 18.39 | 255987 | 235486 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7ST | SA327ST | sa32 7st | sa327st | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 231 | 1649 | Over1500 | 3.3 | 2.42 | 1.77 | 30.73 | 16.39 | 18.12 | 258870 | 233673 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7SY | SA327SY | sa32 7sy | sa327sy | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 648 | 1730 | Over1500 | 3.46 | 2.53 | 1.86 | 32.24 | 17.2 | 19.01 | 258325 | 233242 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7SZ | SA327SZ | sa32 7sz | sa327sz | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 2005 | 1761 | Over1500 | 3.52 | 2.58 | 1.89 | 32.82 | 17.51 | 19.35 | 257503 | 231907 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TA | SA327TA | sa32 7ta | sa327ta | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 1981 | 1761 | Over1500 | 3.52 | 2.58 | 1.89 | 32.82 | 17.51 | 19.35 | 258456 | 231821 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TB | SA327TB | sa32 7tb | sa327tb | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 2031 | 1691 | Over1500 | 3.38 | 2.48 | 1.82 | 31.52 | 16.81 | 18.58 | 259334 | 231871 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TG | SA327TG | sa32 7tg | sa327tg | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 3917 | 1592 | Over1500 | 3.19 | 2.33 | 1.71 | 29.67 | 15.83 | 17.49 | 255875 | 227437 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TH | SA327TH | sa32 7th | sa327th | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 2578 | 1705 | Over1500 | 3.41 | 2.5 | 1.83 | 31.78 | 16.95 | 18.73 | 255896 | 229453 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TJ | SA327TJ | sa32 7tj | sa327tj | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 2348 | 1714 | Over1500 | 3.43 | 2.51 | 1.84 | 31.95 | 17.04 | 18.83 | 256754 | 230015 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TL | SA327TL | sa32 7tl | sa327tl | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 1722 | 1737 | Over1500 | 3.48 | 2.54 | 1.87 | 32.37 | 17.27 | 19.08 | 256911 | 231014 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TN | SA327TN | sa32 7tn | sa327tn | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 2727 | 1727 | Over1500 | 3.46 | 2.53 | 1.85 | 32.19 | 17.17 | 18.97 | 257949 | 230802 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TQ | SA327TQ | sa32 7tq | sa327tq | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 3704 | 1623 | Over1500 | 3.25 | 2.38 | 1.74 | 30.25 | 16.13 | 17.83 | 255779 | 227647 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TR | SA327TR | sa32 7tr | sa327tr | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 3377 | 1607 | Over1500 | 3.22 | 2.35 | 1.73 | 29.95 | 15.97 | 17.66 | 254679 | 227192 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TS | SA327TS | sa32 7ts | sa327ts | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 2345 | 1740 | Over1500 | 3.48 | 2.55 | 1.87 | 32.43 | 17.3 | 19.12 | 254737 | 228522 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TT | SA327TT | sa32 7tt | sa327tt | Carmarthenshire | Sir Gaerfyrddin | Felingwm WwTW | 3353 | 1587 | Over1500 | 3.18 | 2.32 | 1.7 | 29.58 | 15.78 | 17.44 | 253794 | 226038 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TU | SA327TU | sa32 7tu | sa327tu | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 2238 | 1713 | Over1500 | 3.43 | 2.51 | 1.84 | 31.93 | 17.03 | 18.82 | 253532 | 227965 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7TX | SA327TX | sa32 7tx | sa327tx | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 719 | 1752 | Over1500 | 3.51 | 2.57 | 1.88 | 32.65 | 17.42 | 19.25 | 253666 | 229779 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7UA | SA327UA | sa32 7ua | sa327ua | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 3797 | 1623 | Over1500 | 3.25 | 2.38 | 1.74 | 30.25 | 16.13 | 17.83 | 256100 | 227890 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7UB | SA327UB | sa32 7ub | sa327ub | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 4372 | 1577 | Over1500 | 3.16 | 2.31 | 1.69 | 29.39 | 15.68 | 17.33 | 256865 | 227847 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7UE | SA327UE | sa32 7ue | sa327ue | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 4363 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 258098 | 228496 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7UF | SA327UF | sa32 7uf | sa327uf | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 4267 | 1640 | Over1500 | 3.28 | 2.4 | 1.76 | 30.57 | 16.3 | 18.02 | 258574 | 229042 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7UG | SA327UG | sa32 7ug | sa327ug | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 3786 | 1653 | Over1500 | 3.31 | 2.42 | 1.78 | 30.81 | 16.43 | 18.16 | 259714 | 230151 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7UH | SA327UH | sa32 7uh | sa327uh | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 3413 | 1646 | Over1500 | 3.29 | 2.41 | 1.77 | 30.68 | 16.36 | 18.08 | 259231 | 230424 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7UJ | SA327UJ | sa32 7uj | sa327uj | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 3245 | 1709 | Over1500 | 3.42 | 2.5 | 1.84 | 31.85 | 16.99 | 18.78 | 258644 | 230546 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7UL | SA327UL | sa32 7ul | sa327ul | Carmarthenshire | Sir Gaerfyrddin | Bro Nant STW | 3834 | 1612 | Over1500 | 3.23 | 2.36 | 1.73 | 30.05 | 16.02 | 17.71 | 258353 | 229440 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 7UQ | SA327UQ | sa32 7uq | sa327uq | Carmarthenshire | Sir Gaerfyrddin | Abergorlech WwTW | 3082 | 1639 | Over1500 | 3.28 | 2.4 | 1.76 | 30.55 | 16.29 | 18.01 | 260356 | 231210 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8AA | SA328AA | sa32 8aa | sa328aa | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 3029 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 243638 | 220089 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8AB | SA328AB | sa32 8ab | sa328ab | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1806 | 1384 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.8 | 13.76 | 15.21 | 245231 | 220100 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8AD | SA328AD | sa32 8ad | sa328ad | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1890 | 1426 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.58 | 14.18 | 15.67 | 247577 | 220196 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8AE | SA328AE | sa32 8ae | sa328ae | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2318 | 1426 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.58 | 14.18 | 15.67 | 247757 | 219784 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8AG | SA328AG | sa32 8ag | sa328ag | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 1942 | 1421 | 1200to1500 | 2.84 | 2.08 | 1.53 | 26.49 | 14.13 | 15.61 | 246767 | 219690 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8AP | SA328AP | sa32 8ap | sa328ap | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 2956 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 251071 | 218328 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8AT | SA328AT | sa32 8at | sa328at | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 3058 | 1397 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.04 | 13.89 | 15.35 | 243687 | 219949 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8AY | SA328AY | sa32 8ay | sa328ay | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2229 | 1426 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.58 | 14.18 | 15.67 | 248013 | 220168 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8BA | SA328BA | sa32 8ba | sa328ba | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 593 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 257068 | 222099 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8BB | SA328BB | sa32 8bb | sa328bb | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 2141 | 1518 | Over1500 | 3.04 | 2.22 | 1.63 | 28.29 | 15.09 | 16.68 | 255036 | 224751 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8EN | SA328EN | sa32 8en | sa328en | Carmarthenshire | Sir Gaerfyrddin | Glanyrafon STW | 2320 | 1438 | 1200to1500 | 2.88 | 2.11 | 1.54 | 26.8 | 14.29 | 15.8 | 245295 | 219470 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8HG | SA328HG | sa32 8hg | sa328hg | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 3570 | 1491 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.79 | 14.82 | 16.38 | 252213 | 218115 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8HJ | SA328HJ | sa32 8hj | sa328hj | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 2985 | 1439 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.82 | 14.3 | 15.81 | 253204 | 220075 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8HL | SA328HL | sa32 8hl | sa328hl | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 2976 | 1465 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.31 | 14.56 | 16.1 | 251996 | 218677 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8HN | SA328HN | sa32 8hn | sa328hn | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 3381 | 1496 | 1200to1500 | 2.99 | 2.19 | 1.61 | 27.88 | 14.87 | 16.44 | 251456 | 217991 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8HR | SA328HR | sa32 8hr | sa328hr | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 4373 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 252707 | 217474 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8HT | SA328HT | sa32 8ht | sa328ht | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 4579 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 253265 | 217609 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8HU | SA328HU | sa32 8hu | sa328hu | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 4684 | 1595 | Over1500 | 3.19 | 2.34 | 1.71 | 29.73 | 15.86 | 17.52 | 254384 | 218191 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8HX | SA328HX | sa32 8hx | sa328hx | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 4006 | 1552 | Over1500 | 3.11 | 2.27 | 1.67 | 28.93 | 15.43 | 17.05 | 254328 | 218919 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8HY | SA328HY | sa32 8hy | sa328hy | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 3613 | 1499 | 1200to1500 | 3 | 2.2 | 1.61 | 27.94 | 14.9 | 16.47 | 253139 | 218809 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8HZ | SA328HZ | sa32 8hz | sa328hz | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 3929 | 1499 | 1200to1500 | 3 | 2.2 | 1.61 | 27.94 | 14.9 | 16.47 | 253425 | 218656 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JD | SA328JD | sa32 8jd | sa328jd | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 3208 | 1439 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.82 | 14.3 | 15.81 | 253358 | 219871 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JE | SA328JE | sa32 8je | sa328je | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 3276 | 1430 | 1200to1500 | 2.86 | 2.09 | 1.54 | 26.65 | 14.21 | 15.71 | 253532 | 220120 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JF | SA328JF | sa32 8jf | sa328jf | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 3320 | 1430 | 1200to1500 | 2.86 | 2.09 | 1.54 | 26.65 | 14.21 | 15.71 | 253592 | 220096 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JG | SA328JG | sa32 8jg | sa328jg | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 3398 | 1430 | 1200to1500 | 2.86 | 2.09 | 1.54 | 26.65 | 14.21 | 15.71 | 254468 | 219515 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JH | SA328JH | sa32 8jh | sa328jh | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 3242 | 1578 | Over1500 | 3.16 | 2.31 | 1.69 | 29.41 | 15.69 | 17.34 | 255882 | 219467 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JJ | SA328JJ | sa32 8jj | sa328jj | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 2649 | 1486 | 1200to1500 | 2.97 | 2.18 | 1.6 | 27.7 | 14.77 | 16.33 | 256885 | 219687 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JN | SA328JN | sa32 8jn | sa328jn | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 2189 | 1480 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.58 | 14.71 | 16.26 | 257716 | 219555 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JP | SA328JP | sa32 8jp | sa328jp | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 3179 | 1599 | Over1500 | 3.2 | 2.34 | 1.72 | 29.8 | 15.89 | 17.57 | 256622 | 219187 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JQ | SA328JQ | sa32 8jq | sa328jq | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 2822 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 255405 | 219889 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JR | SA328JR | sa32 8jr | sa328jr | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 3407 | 1599 | Over1500 | 3.2 | 2.34 | 1.72 | 29.8 | 15.89 | 17.57 | 256829 | 218694 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JU | SA328JU | sa32 8ju | sa328ju | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 3059 | 1439 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.82 | 14.3 | 15.81 | 253377 | 220344 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JX | SA328JX | sa32 8jx | sa328jx | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1785 | 1451 | 1200to1500 | 2.9 | 2.13 | 1.56 | 27.04 | 14.42 | 15.94 | 252060 | 220454 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8JY | SA328JY | sa32 8jy | sa328jy | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1311 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 250870 | 219977 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8LB | SA328LB | sa32 8lb | sa328lb | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 1415 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 251351 | 220130 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8LD | SA328LD | sa32 8ld | sa328ld | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 2325 | 1465 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.31 | 14.56 | 16.1 | 251647 | 219227 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8LE | SA328LE | sa32 8le | sa328le | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 2660 | 1465 | 1200to1500 | 2.93 | 2.15 | 1.57 | 27.31 | 14.56 | 16.1 | 251728 | 218887 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8LG | SA328LG | sa32 8lg | sa328lg | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 2578 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 251170 | 218743 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8LH | SA328LH | sa32 8lh | sa328lh | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 2595 | 1511 | Over1500 | 3.02 | 2.21 | 1.62 | 28.16 | 15.02 | 16.6 | 250819 | 218649 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8LJ | SA328LJ | sa32 8lj | sa328lj | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 2166 | 1494 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.85 | 14.85 | 16.41 | 250432 | 219051 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8LL | SA328LL | sa32 8ll | sa328ll | Carmarthenshire | Sir Gaerfyrddin | Pont-Ar-Gothi & Nantgaredig WwTW | 2333 | 1451 | 1200to1500 | 2.9 | 2.13 | 1.56 | 27.04 | 14.42 | 15.94 | 252079 | 219551 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8LP | SA328LP | sa32 8lp | sa328lp | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 1348 | 1497 | 1200to1500 | 3 | 2.19 | 1.61 | 27.9 | 14.88 | 16.45 | 259048 | 220042 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8LR | SA328LR | sa32 8lr | sa328lr | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 1719 | 1515 | Over1500 | 3.03 | 2.22 | 1.63 | 28.24 | 15.06 | 16.65 | 259705 | 219855 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8LS | SA328LS | sa32 8ls | sa328ls | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 1555 | 1497 | 1200to1500 | 3 | 2.19 | 1.61 | 27.9 | 14.88 | 16.45 | 258973 | 219830 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8LT | SA328LT | sa32 8lt | sa328lt | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 1851 | 1497 | 1200to1500 | 3 | 2.19 | 1.61 | 27.9 | 14.88 | 16.45 | 258819 | 219536 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8LU | SA328LU | sa32 8lu | sa328lu | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 1940 | 1569 | Over1500 | 3.14 | 2.3 | 1.69 | 29.24 | 15.6 | 17.24 | 259027 | 219447 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8NG | SA328NG | sa32 8ng | sa328ng | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 361 | 1450 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.03 | 14.41 | 15.93 | 258989 | 221030 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8NH | SA328NH | sa32 8nh | sa328nh | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 1036 | 1497 | 1200to1500 | 3 | 2.19 | 1.61 | 27.9 | 14.88 | 16.45 | 258951 | 220349 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8NJ | SA328NJ | sa32 8nj | sa328nj | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 503 | 1450 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.03 | 14.41 | 15.93 | 259276 | 221030 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8NL | SA328NL | sa32 8nl | sa328nl | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 1599 | 1515 | Over1500 | 3.03 | 2.22 | 1.63 | 28.24 | 15.06 | 16.65 | 260091 | 220296 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8NN | SA328NN | sa32 8nn | sa328nn | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 733 | 1502 | Over1500 | 3.01 | 2.2 | 1.61 | 27.99 | 14.93 | 16.5 | 261827 | 220476 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8NW | SA328NW | sa32 8nw | sa328nw | Carmarthenshire | Sir Gaerfyrddin | Ffairfach STW | 1441 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 261110 | 219812 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QD | SA328QD | sa32 8qd | sa328qd | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 809 | 1484 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.66 | 14.75 | 16.3 | 258412 | 222218 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QE | SA328QE | sa32 8qe | sa328qe | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 891 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 258650 | 222233 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QF | SA328QF | sa32 8qf | sa328qf | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 720 | 1464 | 1200to1500 | 2.93 | 2.14 | 1.57 | 27.29 | 14.55 | 16.08 | 258853 | 222101 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QG | SA328QG | sa32 8qg | sa328qg | Carmarthenshire | Sir Gaerfyrddin | Golden Grove WwTW | 693 | 1484 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.66 | 14.75 | 16.3 | 258478 | 221918 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QH | SA328QH | sa32 8qh | sa328qh | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 441 | 1484 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.66 | 14.75 | 16.3 | 257996 | 222119 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QJ | SA328QJ | sa32 8qj | sa328qj | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 448 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 257799 | 222743 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QL | SA328QL | sa32 8ql | sa328ql | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 968 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 256612 | 222806 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QN | SA328QN | sa32 8qn | sa328qn | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 1160 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 256876 | 223232 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QP | SA328QP | sa32 8qp | sa328qp | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 2042 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 257460 | 224372 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QR | SA328QR | sa32 8qr | sa328qr | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 2363 | 1497 | 1200to1500 | 3 | 2.19 | 1.61 | 27.9 | 14.88 | 16.45 | 258550 | 224504 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QS | SA328QS | sa32 8qs | sa328qs | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 2803 | 1504 | Over1500 | 3.01 | 2.2 | 1.62 | 28.03 | 14.95 | 16.52 | 258033 | 225107 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QW | SA328QW | sa32 8qw | sa328qw | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 855 | 1473 | 1200to1500 | 2.95 | 2.16 | 1.58 | 27.45 | 14.64 | 16.18 | 257856 | 223155 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QX | SA328QX | sa32 8qx | sa328qx | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 435 | 1454 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.1 | 14.45 | 15.97 | 255613 | 222267 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8QY | SA328QY | sa32 8qy | sa328qy | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 423 | 1454 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.1 | 14.45 | 15.97 | 255805 | 222306 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RA | SA328RA | sa32 8ra | sa328ra | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 687 | 1454 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.1 | 14.45 | 15.97 | 255722 | 222017 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RB | SA328RB | sa32 8rb | sa328rb | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1192 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 255471 | 221522 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RD | SA328RD | sa32 8rd | sa328rd | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1002 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 255133 | 221842 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RE | SA328RE | sa32 8re | sa328re | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1265 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 254526 | 222120 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RF | SA328RF | sa32 8rf | sa328rf | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1355 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 254646 | 221791 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RG | SA328RG | sa32 8rg | sa328rg | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 2097 | 1428 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.62 | 14.2 | 15.69 | 253862 | 221604 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RH | SA328RH | sa32 8rh | sa328rh | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 2477 | 1406 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.21 | 13.98 | 15.45 | 254183 | 220704 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RJ | SA328RJ | sa32 8rj | sa328rj | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1622 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 255147 | 221158 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RL | SA328RL | sa32 8rl | sa328rl | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1423 | 1449 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.01 | 14.4 | 15.92 | 255579 | 221279 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RN | SA328RN | sa32 8rn | sa328rn | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1945 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 255343 | 220780 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RP | SA328RP | sa32 8rp | sa328rp | Carmarthenshire | Sir Gaerfyrddin | Broad Oak WwTW | 1402 | 1458 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.17 | 14.49 | 16.02 | 257252 | 220981 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RT | SA328RT | sa32 8rt | sa328rt | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 507 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 255616 | 223206 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RU | SA328RU | sa32 8ru | sa328ru | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 151 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 255800 | 222720 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RW | SA328RW | sa32 8rw | sa328rw | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 2079 | 1449 | 1200to1500 | 2.9 | 2.12 | 1.56 | 27.01 | 14.4 | 15.92 | 255849 | 220631 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RX | SA328RX | sa32 8rx | sa328rx | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 466 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 255505 | 223143 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8RY | SA328RY | sa32 8ry | sa328ry | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 474 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 255569 | 223167 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8SA | SA328SA | sa32 8sa | sa328sa | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 576 | 1454 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.1 | 14.45 | 15.97 | 255183 | 223037 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8SB | SA328SB | sa32 8sb | sa328sb | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1139 | 1454 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.1 | 14.45 | 15.97 | 254513 | 222760 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8SD | SA328SD | sa32 8sd | sa328sd | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1070 | 1491 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.79 | 14.82 | 16.38 | 255212 | 223676 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8SE | SA328SE | sa32 8se | sa328se | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1391 | 1491 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.79 | 14.82 | 16.38 | 254595 | 223606 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8SF | SA328SF | sa32 8sf | sa328sf | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1713 | 1491 | 1200to1500 | 2.98 | 2.18 | 1.6 | 27.79 | 14.82 | 16.38 | 254646 | 224088 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8SG | SA328SG | sa32 8sg | sa328sg | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 2462 | 1518 | Over1500 | 3.04 | 2.22 | 1.63 | 28.29 | 15.09 | 16.68 | 255467 | 225155 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8SH | SA328SH | sa32 8sh | sa328sh | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 623 | 1441 | 1200to1500 | 2.88 | 2.11 | 1.55 | 26.86 | 14.32 | 15.83 | 255929 | 223257 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8SJ | SA328SJ | sa32 8sj | sa328sj | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1384 | 1501 | Over1500 | 3 | 2.2 | 1.61 | 27.98 | 14.92 | 16.49 | 255969 | 224047 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8SL | SA328SL | sa32 8sl | sa328sl | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 2883 | 1554 | Over1500 | 3.11 | 2.28 | 1.67 | 28.96 | 15.45 | 17.07 | 256332 | 225501 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA32 8SN | SA328SN | sa32 8sn | sa328sn | Carmarthenshire | Sir Gaerfyrddin | Cwrt Henri STW | 1706 | 1481 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.6 | 14.72 | 16.27 | 253970 | 222995 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5DJ | SA335DJ | sa33 5dj | sa335dj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 7354 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 236737 | 218386 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5DP | SA335DP | sa33 5dp | sa335dp | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 6628 | 1396 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26.02 | 13.88 | 15.34 | 237227 | 218922 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5DR | SA335DR | sa33 5dr | sa335dr | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5909 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 237980 | 219209 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5DS | SA335DS | sa33 5ds | sa335ds | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 6306 | 1434 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.73 | 14.25 | 15.76 | 237050 | 219576 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5ER | SA335ER | sa33 5er | sa335er | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5701 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 238218 | 219282 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5ES | SA335ES | sa33 5es | sa335es | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 6350 | 1396 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26.02 | 13.88 | 15.34 | 237499 | 219047 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 5YL | SA335YL | sa33 5yl | sa335yl | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 4301 | 1352 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.2 | 13.44 | 14.85 | 241300 | 219431 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6AA | SA336AA | sa33 6aa | sa336aa | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 3866 | 1540 | Over1500 | 3.08 | 2.26 | 1.65 | 28.7 | 15.31 | 16.92 | 238296 | 222111 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6AG | SA336AG | sa33 6ag | sa336ag | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5083 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 237318 | 221341 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6AJ | SA336AJ | sa33 6aj | sa336aj | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 5059 | 1575 | Over1500 | 3.15 | 2.31 | 1.69 | 29.36 | 15.66 | 17.3 | 237078 | 221939 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6AN | SA336AN | sa33 6an | sa336an | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 145 | 1620 | Over1500 | 3.24 | 2.37 | 1.74 | 30.19 | 16.1 | 17.8 | 237765 | 226872 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6AR | SA336AR | sa33 6ar | sa336ar | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 1709 | 1621 | Over1500 | 3.24 | 2.37 | 1.74 | 30.21 | 16.11 | 17.81 | 238967 | 225861 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6AS | SA336AS | sa33 6as | sa336as | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 996 | 1711 | Over1500 | 3.42 | 2.51 | 1.84 | 31.89 | 17.01 | 18.8 | 237312 | 229875 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6AX | SA336AX | sa33 6ax | sa336ax | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 4366 | 1852 | Over1500 | 3.71 | 2.71 | 1.99 | 34.52 | 18.41 | 20.35 | 235014 | 234110 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BA | SA336BA | sa33 6ba | sa336ba | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1241 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 242050 | 224919 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BB | SA336BB | sa33 6bb | sa336bb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 901 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 241944 | 222808 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BD | SA336BD | sa33 6bd | sa336bd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 682 | 1505 | Over1500 | 3.01 | 2.2 | 1.62 | 28.05 | 14.96 | 16.54 | 241838 | 224382 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BE | SA336BE | sa33 6be | sa336be | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1232 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 241959 | 224924 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BG | SA336BG | sa33 6bg | sa336bg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2457 | 1580 | Over1500 | 3.16 | 2.31 | 1.7 | 29.45 | 15.71 | 17.36 | 242508 | 226058 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BH | SA336BH | sa33 6bh | sa336bh | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2971 | 1580 | Over1500 | 3.16 | 2.31 | 1.7 | 29.45 | 15.71 | 17.36 | 243157 | 226353 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BJ | SA336BJ | sa33 6bj | sa336bj | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 2445 | 1599 | Over1500 | 3.2 | 2.34 | 1.72 | 29.8 | 15.89 | 17.57 | 242888 | 227101 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BL | SA336BL | sa33 6bl | sa336bl | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 3056 | 1622 | Over1500 | 3.25 | 2.38 | 1.74 | 30.23 | 16.12 | 17.82 | 243772 | 227053 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BN | SA336BN | sa33 6bn | sa336bn | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 2289 | 1606 | Over1500 | 3.21 | 2.35 | 1.72 | 29.93 | 15.96 | 17.64 | 241912 | 226882 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BP | SA336BP | sa33 6bp | sa336bp | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 598 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 241687 | 228560 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BQ | SA336BQ | sa33 6bq | sa336bq | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 578 | 1628 | Over1500 | 3.26 | 2.38 | 1.75 | 30.34 | 16.18 | 17.89 | 241516 | 229717 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BS | SA336BS | sa33 6bs | sa336bs | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 204 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 241631 | 228958 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BT | SA336BT | sa33 6bt | sa336bt | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 436 | 1628 | Over1500 | 3.26 | 2.38 | 1.75 | 30.34 | 16.18 | 17.89 | 241542 | 229576 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BU | SA336BU | sa33 6bu | sa336bu | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 702 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 241420 | 229832 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BW | SA336BW | sa33 6bw | sa336bw | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 370 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 241865 | 228963 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BX | SA336BX | sa33 6bx | sa336bx | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 323 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 241745 | 228891 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BY | SA336BY | sa33 6by | sa336by | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 426 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 241945 | 229008 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6BZ | SA336BZ | sa33 6bz | sa336bz | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 292 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 241783 | 229301 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6DA | SA336DA | sa33 6da | sa336da | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 546 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 242046 | 229345 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6DB | SA336DB | sa33 6db | sa336db | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 894 | 1559 | Over1500 | 3.12 | 2.28 | 1.67 | 29.06 | 15.5 | 17.13 | 242406 | 229363 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6DD | SA336DD | sa33 6dd | sa336dd | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 1939 | 1560 | Over1500 | 3.12 | 2.28 | 1.68 | 29.08 | 15.51 | 17.14 | 244194 | 229364 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6EE | SA336EE | sa33 6ee | sa336ee | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 2206 | 1492 | 1200to1500 | 2.99 | 2.19 | 1.6 | 27.81 | 14.83 | 16.39 | 240096 | 222324 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6EJ | SA336EJ | sa33 6ej | sa336ej | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 1490 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 237698 | 225506 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6EL | SA336EL | sa33 6el | sa336el | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 1026 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 237814 | 225978 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6EP | SA336EP | sa33 6ep | sa336ep | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 1880 | 1711 | Over1500 | 3.42 | 2.51 | 1.84 | 31.89 | 17.01 | 18.8 | 236406 | 225622 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6EQ | SA336EQ | sa33 6eq | sa336eq | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1546 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 240326 | 224096 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6ER | SA336ER | sa33 6er | sa336er | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 1841 | 1711 | Over1500 | 3.42 | 2.51 | 1.84 | 31.89 | 17.01 | 18.8 | 235969 | 226339 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6ES | SA336ES | sa33 6es | sa336es | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 2735 | 1713 | Over1500 | 3.43 | 2.51 | 1.84 | 31.93 | 17.03 | 18.82 | 234978 | 226635 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6HD | SA336HD | sa33 6hd | sa336hd | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 2549 | 1715 | Over1500 | 3.43 | 2.51 | 1.84 | 31.96 | 17.05 | 18.84 | 235759 | 225331 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6HH | SA336HH | sa33 6hh | sa336hh | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 2560 | 1683 | Over1500 | 3.37 | 2.46 | 1.81 | 31.37 | 16.73 | 18.49 | 235442 | 225769 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6HL | SA336HL | sa33 6hl | sa336hl | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 1988 | 1606 | Over1500 | 3.21 | 2.35 | 1.72 | 29.93 | 15.96 | 17.64 | 242064 | 227223 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6HN | SA336HN | sa33 6hn | sa336hn | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 2569 | 1620 | Over1500 | 3.24 | 2.37 | 1.74 | 30.19 | 16.1 | 17.8 | 240550 | 226770 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6HT | SA336HT | sa33 6ht | sa336ht | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 137 | 1505 | Over1500 | 3.01 | 2.2 | 1.62 | 28.05 | 14.96 | 16.54 | 241752 | 223819 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6HU | SA336HU | sa33 6hu | sa336hu | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 305 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 241751 | 223403 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6HX | SA336HX | sa33 6hx | sa336hx | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 190 | 1505 | Over1500 | 3.01 | 2.2 | 1.62 | 28.05 | 14.96 | 16.54 | 242008 | 223729 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6HY | SA336HY | sa33 6hy | sa336hy | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 685 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 242343 | 223257 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JA | SA336JA | sa33 6ja | sa336ja | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 194 | 1505 | Over1500 | 3.01 | 2.2 | 1.62 | 28.05 | 14.96 | 16.54 | 241659 | 223809 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JB | SA336JB | sa33 6jb | sa336jb | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 173 | 1505 | Over1500 | 3.01 | 2.2 | 1.62 | 28.05 | 14.96 | 16.54 | 241698 | 223823 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JD | SA336JD | sa33 6jd | sa336jd | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 555 | 1498 | 1200to1500 | 3 | 2.19 | 1.61 | 27.92 | 14.89 | 16.46 | 241490 | 224146 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JE | SA336JE | sa33 6je | sa336je | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1251 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 241144 | 224753 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JF | SA336JF | sa33 6jf | sa336jf | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1373 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 241033 | 224825 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JG | SA336JG | sa33 6jg | sa336jg | Carmarthenshire | Sir Gaerfyrddin | Bronwydd STW | 1947 | 1531 | Over1500 | 3.06 | 2.24 | 1.64 | 28.54 | 15.22 | 16.82 | 241006 | 225468 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JL | SA336JL | sa33 6jl | sa336jl | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 1208 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 240978 | 230209 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JN | SA336JN | sa33 6jn | sa336jn | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 1309 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 241213 | 230407 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JP | SA336JP | sa33 6jp | sa336jp | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 1074 | 1628 | Over1500 | 3.26 | 2.38 | 1.75 | 30.34 | 16.18 | 17.89 | 241562 | 230214 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JR | SA336JR | sa33 6jr | sa336jr | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 1940 | 1696 | Over1500 | 3.39 | 2.48 | 1.82 | 31.61 | 16.86 | 18.63 | 241533 | 231080 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JS | SA336JS | sa33 6js | sa336js | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 1365 | 1628 | Over1500 | 3.26 | 2.38 | 1.75 | 30.34 | 16.18 | 17.89 | 242277 | 230289 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JT | SA336JT | sa33 6jt | sa336jt | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 2478 | 1747 | Over1500 | 3.5 | 2.56 | 1.88 | 32.56 | 17.37 | 19.19 | 241955 | 232100 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JU | SA336JU | sa33 6ju | sa336ju | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 1810 | 1684 | Over1500 | 3.37 | 2.47 | 1.81 | 31.39 | 16.74 | 18.5 | 242508 | 231050 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6JX | SA336JX | sa33 6jx | sa336jx | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 1745 | 1660 | Over1500 | 3.32 | 2.43 | 1.78 | 30.94 | 16.5 | 18.24 | 243194 | 229950 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LA | SA336LA | sa33 6la | sa336la | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 507 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 241305 | 229589 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LB | SA336LB | sa33 6lb | sa336lb | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 1548 | 1678 | Over1500 | 3.36 | 2.46 | 1.8 | 31.28 | 16.68 | 18.44 | 240361 | 230143 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LD | SA336LD | sa33 6ld | sa336ld | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 1587 | 1678 | Over1500 | 3.36 | 2.46 | 1.8 | 31.28 | 16.68 | 18.44 | 240016 | 229582 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LE | SA336LE | sa33 6le | sa336le | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 2063 | 1678 | Over1500 | 3.36 | 2.46 | 1.8 | 31.28 | 16.68 | 18.44 | 239805 | 230256 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LG | SA336LG | sa33 6lg | sa336lg | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 2664 | 1901 | Over1500 | 3.8 | 2.78 | 2.04 | 35.43 | 18.9 | 20.89 | 239941 | 232324 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LH | SA336LH | sa33 6lh | sa336lh | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 2693 | 1776 | Over1500 | 3.55 | 2.6 | 1.91 | 33.1 | 17.65 | 19.51 | 241095 | 231796 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LJ | SA336LJ | sa33 6lj | sa336lj | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 436 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 241364 | 229539 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LN | SA336LN | sa33 6ln | sa336ln | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 516 | 1628 | Over1500 | 3.26 | 2.38 | 1.75 | 30.34 | 16.18 | 17.89 | 241504 | 229655 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LP | SA336LP | sa33 6lp | sa336lp | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 613 | 1565 | Over1500 | 3.13 | 2.29 | 1.68 | 29.17 | 15.56 | 17.19 | 240932 | 229216 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LR | SA336LR | sa33 6lr | sa336lr | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 134 | 1565 | Over1500 | 3.13 | 2.29 | 1.68 | 29.17 | 15.56 | 17.19 | 241430 | 229063 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LS | SA336LS | sa33 6ls | sa336ls | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 759 | 1638 | Over1500 | 3.28 | 2.4 | 1.76 | 30.53 | 16.28 | 18 | 241205 | 228459 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LT | SA336LT | sa33 6lt | sa336lt | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 1824 | 1604 | Over1500 | 3.21 | 2.35 | 1.72 | 29.9 | 15.94 | 17.62 | 240484 | 227653 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6LX | SA336LX | sa33 6lx | sa336lx | Carmarthenshire | Sir Gaerfyrddin | Llanpumpsaint WwTW | 1686 | 1564 | Over1500 | 3.13 | 2.29 | 1.68 | 29.15 | 15.55 | 17.18 | 242737 | 227953 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6SP | SA336SP | sa33 6sp | sa336sp | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 1916 | 1613 | Over1500 | 3.23 | 2.36 | 1.73 | 30.06 | 16.03 | 17.72 | 236812 | 228699 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6SR | SA336SR | sa33 6sr | sa336sr | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 1509 | 1847 | Over1500 | 3.7 | 2.71 | 1.98 | 34.43 | 18.36 | 20.29 | 236315 | 231035 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6SS | SA336SS | sa33 6ss | sa336ss | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 2553 | 1807 | Over1500 | 3.62 | 2.65 | 1.94 | 33.68 | 17.96 | 19.85 | 235678 | 232170 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6ST | SA336ST | sa33 6st | sa336st | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 3481 | 1845 | Over1500 | 3.69 | 2.7 | 1.98 | 34.39 | 18.34 | 20.27 | 234380 | 231412 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6SU | SA336SU | sa33 6su | sa336su | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 4264 | 1933 | Over1500 | 3.87 | 2.83 | 2.08 | 36.03 | 19.21 | 21.24 | 234250 | 233113 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6SW | SA336SW | sa33 6sw | sa336sw | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 938 | 1650 | Over1500 | 3.3 | 2.42 | 1.77 | 30.75 | 16.4 | 18.13 | 237194 | 227793 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6SX | SA336SX | sa33 6sx | sa336sx | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 4601 | 1931 | Over1500 | 3.86 | 2.83 | 2.07 | 35.99 | 19.2 | 21.22 | 233419 | 233970 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6SY | SA336SY | sa33 6sy | sa336sy | Carmarthenshire | Sir Gaerfyrddin | Capel Iwan STW | 4852 | 1888 | Over1500 | 3.78 | 2.77 | 2.03 | 35.19 | 18.77 | 20.74 | 232813 | 232683 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6SZ | SA336SZ | sa33 6sz | sa336sz | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 5463 | 1835 | Over1500 | 3.67 | 2.69 | 1.97 | 34.2 | 18.24 | 20.16 | 232389 | 231526 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TH | SA336TH | sa33 6th | sa336th | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 650 | 1642 | Over1500 | 3.29 | 2.4 | 1.76 | 30.6 | 16.32 | 18.04 | 237191 | 227413 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TL | SA336TL | sa33 6tl | sa336tl | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 637 | 1642 | Over1500 | 3.29 | 2.4 | 1.76 | 30.6 | 16.32 | 18.04 | 237295 | 227496 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TN | SA336TN | sa33 6tn | sa336tn | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 481 | 1642 | Over1500 | 3.29 | 2.4 | 1.76 | 30.6 | 16.32 | 18.04 | 237324 | 227309 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TP | SA336TP | sa33 6tp | sa336tp | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 75 | 1620 | Over1500 | 3.24 | 2.37 | 1.74 | 30.19 | 16.1 | 17.8 | 237691 | 226921 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TQ | SA336TQ | sa33 6tq | sa336tq | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 137 | 1620 | Over1500 | 3.24 | 2.37 | 1.74 | 30.19 | 16.1 | 17.8 | 237552 | 227005 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TR | SA336TR | sa33 6tr | sa336tr | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 767 | 1650 | Over1500 | 3.3 | 2.42 | 1.77 | 30.75 | 16.4 | 18.13 | 237259 | 227631 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TS | SA336TS | sa33 6ts | sa336ts | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 741 | 1650 | Over1500 | 3.3 | 2.42 | 1.77 | 30.75 | 16.4 | 18.13 | 237360 | 227660 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TT | SA336TT | sa33 6tt | sa336tt | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 646 | 1642 | Over1500 | 3.29 | 2.4 | 1.76 | 30.6 | 16.32 | 18.04 | 237267 | 227485 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TU | SA336TU | sa33 6tu | sa336tu | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 853 | 1642 | Over1500 | 3.29 | 2.4 | 1.76 | 30.6 | 16.32 | 18.04 | 236969 | 227454 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TW | SA336TW | sa33 6tw | sa336tw | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 894 | 1650 | Over1500 | 3.3 | 2.42 | 1.77 | 30.75 | 16.4 | 18.13 | 237181 | 227732 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TX | SA336TX | sa33 6tx | sa336tx | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 1630 | 1688 | Over1500 | 3.38 | 2.47 | 1.81 | 31.46 | 16.78 | 18.55 | 236069 | 227174 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TY | SA336TY | sa33 6ty | sa336ty | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 1438 | 1671 | Over1500 | 3.34 | 2.45 | 1.79 | 31.14 | 16.61 | 18.36 | 236407 | 227648 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6TZ | SA336TZ | sa33 6tz | sa336tz | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 2965 | 1753 | Over1500 | 3.51 | 2.57 | 1.88 | 32.67 | 17.43 | 19.26 | 235332 | 228794 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6UA | SA336UA | sa33 6ua | sa336ua | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 3397 | 1753 | Over1500 | 3.51 | 2.57 | 1.88 | 32.67 | 17.43 | 19.26 | 234731 | 229280 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6UB | SA336UB | sa33 6ub | sa336ub | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 3522 | 1814 | Over1500 | 3.63 | 2.66 | 1.95 | 33.81 | 18.03 | 19.93 | 234393 | 229837 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6UD | SA336UD | sa33 6ud | sa336ud | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 3628 | 1814 | Over1500 | 3.63 | 2.66 | 1.95 | 33.81 | 18.03 | 19.93 | 234274 | 229877 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6UH | SA336UH | sa33 6uh | sa336uh | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 382 | 1620 | Over1500 | 3.24 | 2.37 | 1.74 | 30.19 | 16.1 | 17.8 | 237504 | 227330 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6UJ | SA336UJ | sa33 6uj | sa336uj | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 1144 | 1650 | Over1500 | 3.3 | 2.42 | 1.77 | 30.75 | 16.4 | 18.13 | 237436 | 228112 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6UL | SA336UL | sa33 6ul | sa336ul | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 1783 | 1613 | Over1500 | 3.23 | 2.36 | 1.73 | 30.06 | 16.03 | 17.72 | 237496 | 228768 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6UN | SA336UN | sa33 6un | sa336un | Carmarthenshire | Sir Gaerfyrddin | Cynwyl Elfed WwTW | 1948 | 1635 | Over1500 | 3.27 | 2.39 | 1.76 | 30.47 | 16.25 | 17.96 | 238756 | 228626 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6UP | SA336UP | sa33 6up | sa336up | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 1809 | 1618 | Over1500 | 3.24 | 2.37 | 1.74 | 30.16 | 16.08 | 17.78 | 237732 | 228937 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6UR | SA336UR | sa33 6ur | sa336ur | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 1562 | 1701 | Over1500 | 3.4 | 2.49 | 1.83 | 31.7 | 16.91 | 18.69 | 239255 | 230188 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6UT | SA336UT | sa33 6ut | sa336ut | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 1399 | 1701 | Over1500 | 3.4 | 2.49 | 1.83 | 31.7 | 16.91 | 18.69 | 239147 | 230381 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6UU | SA336UU | sa33 6uu | sa336uu | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 1263 | 1711 | Over1500 | 3.42 | 2.51 | 1.84 | 31.89 | 17.01 | 18.8 | 237448 | 229531 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6XA | SA336XA | sa33 6xa | sa336xa | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 788 | 1730 | Over1500 | 3.46 | 2.53 | 1.86 | 32.24 | 17.2 | 19.01 | 237555 | 231495 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6XB | SA336XB | sa33 6xb | sa336xb | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 1865 | 1839 | Over1500 | 3.68 | 2.69 | 1.98 | 34.28 | 18.28 | 20.2 | 238838 | 232292 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6XD | SA336XD | sa33 6xd | sa336xd | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 1900 | 1839 | Over1500 | 3.68 | 2.69 | 1.98 | 34.28 | 18.28 | 20.2 | 239185 | 232041 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6XG | SA336XG | sa33 6xg | sa336xg | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 2512 | 1877 | Over1500 | 3.76 | 2.75 | 2.02 | 34.98 | 18.66 | 20.62 | 238179 | 233227 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6XJ | SA336XJ | sa33 6xj | sa336xj | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 451 | 1730 | Over1500 | 3.46 | 2.53 | 1.86 | 32.24 | 17.2 | 19.01 | 237642 | 231169 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6XL | SA336XL | sa33 6xl | sa336xl | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 145 | 1730 | Over1500 | 3.46 | 2.53 | 1.86 | 32.24 | 17.2 | 19.01 | 237751 | 230883 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6XN | SA336XN | sa33 6xn | sa336xn | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 758 | 1776 | Over1500 | 3.55 | 2.6 | 1.91 | 33.1 | 17.65 | 19.51 | 237291 | 231310 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6XP | SA336XP | sa33 6xp | sa336xp | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 2212 | 1826 | Over1500 | 3.65 | 2.67 | 1.96 | 34.03 | 18.15 | 20.06 | 236615 | 232615 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6XR | SA336XR | sa33 6xr | sa336xr | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 1196 | 1791 | Over1500 | 3.58 | 2.62 | 1.92 | 33.38 | 17.8 | 19.68 | 237830 | 231940 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA33 6XT | SA336XT | sa33 6xt | sa336xt | Carmarthenshire | Sir Gaerfyrddin | Cwmduad STW | 217 | 1730 | Over1500 | 3.46 | 2.53 | 1.86 | 32.24 | 17.2 | 19.01 | 237713 | 230945 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9DB | SA399DB | sa39 9db | sa399db | Carmarthenshire | Sir Gaerfyrddin | Alltwalis STW | 3462 | 1812 | Over1500 | 3.63 | 2.65 | 1.95 | 33.77 | 18.01 | 19.91 | 241462 | 233283 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9ED | SA399ED | sa39 9ed | sa399ed | Carmarthenshire | Sir Gaerfyrddin | Bryndulais STW | 4177 | 1793 | Over1500 | 3.59 | 2.63 | 1.93 | 33.42 | 17.82 | 19.7 | 251484 | 236703 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA39 9EJ | SA399EJ | sa39 9ej | sa399ej | Carmarthenshire | Sir Gaerfyrddin | Brechfa WwTW | 5120 | 1776 | Over1500 | 3.55 | 2.6 | 1.91 | 33.1 | 17.65 | 19.51 | 250655 | 234674 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8EZ | SA488EZ | sa48 8ez | sa488ez | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 3252 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 260199 | 244196 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HA | SA488HA | sa48 8ha | sa488ha | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 3281 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 260254 | 243512 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HB | SA488HB | sa48 8hb | sa488hb | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 2768 | 1515 | Over1500 | 3.03 | 2.22 | 1.63 | 28.24 | 15.06 | 16.65 | 260686 | 244109 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HD | SA488HD | sa48 8hd | sa488hd | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 2635 | 1515 | Over1500 | 3.03 | 2.22 | 1.63 | 28.24 | 15.06 | 16.65 | 260915 | 243534 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HE | SA488HE | sa48 8he | sa488he | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 2105 | 1553 | Over1500 | 3.11 | 2.27 | 1.67 | 28.95 | 15.44 | 17.06 | 261641 | 243174 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HF | SA488HF | sa48 8hf | sa488hf | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 2016 | 1545 | Over1500 | 3.09 | 2.26 | 1.66 | 28.8 | 15.36 | 16.97 | 261503 | 243727 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA48 8HG | SA488HG | sa48 8hg | sa488hg | Carmarthenshire | Sir Gaerfyrddin | Heol Timothy STW | 2582 | 1515 | Over1500 | 3.03 | 2.22 | 1.63 | 28.24 | 15.06 | 16.65 | 260876 | 244448 | Carmarthenshire LPA | CA | Afon Tywi/ River Tywi | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SY25 6NP | SY256NP | sy25 6np | sy256np | Ceredigion | Sir Ceredigion | Tregaron WwTW | 10732 | 1841 | Over1500 | 3.68 | 2.7 | 1.98 | 34.31 | 18.3 | 20.23 | 277317 | 255423 | Ceredigion LPA | CE | Afon Tywi/ River Tywi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6NR | SY256NR | sy25 6nr | sy256nr | Powys | Powys | Beulah STW | 12350 | 1937 | Over1500 | 3.88 | 2.84 | 2.08 | 36.1 | 19.25 | 21.28 | 280897 | 255959 | Powys LPA | PO | Afon Tywi/ River Tywi | Cyngor Sir Powys | Powys County Council
SY25 6NW | SY256NW | sy25 6nw | sy256nw | Ceredigion | Sir Ceredigion | Pontrhydfendigaid WwTW | 8945 | 1847 | Over1500 | 3.7 | 2.71 | 1.98 | 34.43 | 18.36 | 20.29 | 276201 | 258445 | Ceredigion LPA | CE | Afon Tywi/ River Tywi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PG | SY256PG | sy25 6pg | sy256pg | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 6474 | 1734 | Over1500 | 3.47 | 2.54 | 1.86 | 32.32 | 17.24 | 19.05 | 271627 | 252538 | Ceredigion LPA | CE | Afon Tywi/ River Tywi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PH | SY256PH | sy25 6ph | sy256ph | Ceredigion | Sir Ceredigion | Llandewi Brefi WwTW | 9513 | 1771 | Over1500 | 3.54 | 2.59 | 1.9 | 33.01 | 17.6 | 19.46 | 275071 | 253449 | Ceredigion LPA | CE | Afon Tywi/ River Tywi | Cyngor Sir Ceredigion | Ceredigion County Council
SY25 6PQ | SY256PQ | sy25 6pq | sy256pq | Ceredigion | Sir Ceredigion | Rhandirmwyn STW | 8475 | 1775 | Over1500 | 3.55 | 2.6 | 1.91 | 33.08 | 17.64 | 19.5 | 274407 | 250874 | Ceredigion LPA | CE | Afon Tywi/ River Tywi | Cyngor Sir Ceredigion | Ceredigion County Council
SA34 0UD | SA340UD | sa34 0ud | sa340ud | Pembrokeshire | Sir Benfro | Llangolman STW | 5332 | 1749 | Over1500 | 3.5 | 2.56 | 1.88 | 32.6 | 17.39 | 19.22 | 217281 | 229756 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA34 0YL | SA340YL | sa34 0yl | sa340yl | Carmarthenshire | Sir Gaerfyrddin | Llangolman STW | 4672 | 1708 | Over1500 | 3.42 | 2.5 | 1.83 | 31.83 | 16.98 | 18.77 | 216953 | 228926 | Carmarthenshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA34 0YP | SA340YP | sa34 0yp | sa340yp | Carmarthenshire | Sir Gaerfyrddin | Llangolman STW | 3776 | 1649 | Over1500 | 3.3 | 2.42 | 1.77 | 30.73 | 16.39 | 18.12 | 216177 | 228451 | Carmarthenshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA61 1AE | SA611AE | sa61 1ae | sa611ae | Pembrokeshire | Sir Benfro | Camrose WwTW | 5118 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195032 | 215591 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1AT | SA611AT | sa61 1at | sa611at | Pembrokeshire | Sir Benfro | Keeston WwTW | 5112 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194739 | 215401 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BA | SA611BA | sa61 1ba | sa611ba | Pembrokeshire | Sir Benfro | Camrose WwTW | 5311 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195493 | 215652 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BB | SA611BB | sa61 1bb | sa611bb | Pembrokeshire | Sir Benfro | Camrose WwTW | 5460 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195522 | 215492 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BD | SA611BD | sa61 1bd | sa611bd | Pembrokeshire | Sir Benfro | Camrose WwTW | 5405 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195484 | 215532 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BE | SA611BE | sa61 1be | sa611be | Pembrokeshire | Sir Benfro | Camrose WwTW | 5608 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195567 | 215344 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BG | SA611BG | sa61 1bg | sa611bg | Pembrokeshire | Sir Benfro | Camrose WwTW | 5345 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195467 | 215593 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BH | SA611BH | sa61 1bh | sa611bh | Pembrokeshire | Sir Benfro | Camrose WwTW | 5433 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195521 | 215524 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BN | SA611BN | sa61 1bn | sa611bn | Pembrokeshire | Sir Benfro | Keeston WwTW | 5116 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194665 | 215308 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BP | SA611BP | sa61 1bp | sa611bp | Pembrokeshire | Sir Benfro | Keeston WwTW | 4938 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194533 | 215427 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BS | SA611BS | sa61 1bs | sa611bs | Pembrokeshire | Sir Benfro | Keeston WwTW | 4975 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194458 | 215289 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BT | SA611BT | sa61 1bt | sa611bt | Pembrokeshire | Sir Benfro | Keeston WwTW | 4924 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194415 | 215317 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BU | SA611BU | sa61 1bu | sa611bu | Pembrokeshire | Sir Benfro | Keeston WwTW | 5251 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194757 | 215208 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BW | SA611BW | sa61 1bw | sa611bw | Pembrokeshire | Sir Benfro | Keeston WwTW | 5094 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194665 | 215341 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BX | SA611BX | sa61 1bx | sa611bx | Pembrokeshire | Sir Benfro | Keeston WwTW | 4702 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194256 | 215473 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BY | SA611BY | sa61 1by | sa611by | Pembrokeshire | Sir Benfro | Keeston WwTW | 4781 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194443 | 215563 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1BZ | SA611BZ | sa61 1bz | sa611bz | Pembrokeshire | Sir Benfro | Keeston WwTW | 5012 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194647 | 215447 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DG | SA611DG | sa61 1dg | sa611dg | Pembrokeshire | Sir Benfro | Keeston WwTW | 3904 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 193015 | 215452 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1DP | SA611DP | sa61 1dp | sa611dp | Pembrokeshire | Sir Benfro | Keeston WwTW | 4242 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193585 | 215464 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EA | SA611EA | sa61 1ea | sa611ea | Pembrokeshire | Sir Benfro | Keeston WwTW | 4641 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 194147 | 215447 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1EG | SA611EG | sa61 1eg | sa611eg | Pembrokeshire | Sir Benfro | Keeston WwTW | 5154 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194624 | 215205 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NE | SA611NE | sa61 1ne | sa611ne | Pembrokeshire | Sir Benfro | Camrose WwTW | 5624 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195163 | 215086 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NF | SA611NF | sa61 1nf | sa611nf | Pembrokeshire | Sir Benfro | Camrose WwTW | 5294 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195228 | 215502 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NH | SA611NH | sa61 1nh | sa611nh | Pembrokeshire | Sir Benfro | Camrose WwTW | 5306 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195262 | 215509 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NJ | SA611NJ | sa61 1nj | sa611nj | Pembrokeshire | Sir Benfro | Camrose WwTW | 5281 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195166 | 215481 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NL | SA611NL | sa61 1nl | sa611nl | Pembrokeshire | Sir Benfro | Camrose WwTW | 5321 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195217 | 215464 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NP | SA611NP | sa61 1np | sa611np | Pembrokeshire | Sir Benfro | Camrose WwTW | 5334 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195167 | 215420 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NQ | SA611NQ | sa61 1nq | sa611nq | Pembrokeshire | Sir Benfro | Camrose WwTW | 5275 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195247 | 215536 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NR | SA611NR | sa61 1nr | sa611nr | Pembrokeshire | Sir Benfro | Camrose WwTW | 5387 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195091 | 215316 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NS | SA611NS | sa61 1ns | sa611ns | Pembrokeshire | Sir Benfro | Camrose WwTW | 5448 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195023 | 215211 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NT | SA611NT | sa61 1nt | sa611nt | Pembrokeshire | Sir Benfro | Keeston WwTW | 5593 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195093 | 215074 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NU | SA611NU | sa61 1nu | sa611nu | Pembrokeshire | Sir Benfro | Camrose WwTW | 5589 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195124 | 215104 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1NX | SA611NX | sa61 1nx | sa611nx | Pembrokeshire | Sir Benfro | Keeston WwTW | 5623 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195072 | 215003 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PB | SA611PB | sa61 1pb | sa611pb | Pembrokeshire | Sir Benfro | Keeston WwTW | 5570 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195029 | 215035 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PE | SA611PE | sa61 1pe | sa611pe | Pembrokeshire | Sir Benfro | Keeston WwTW | 5470 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194971 | 215120 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PG | SA611PG | sa61 1pg | sa611pg | Pembrokeshire | Sir Benfro | Keeston WwTW | 5424 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194886 | 215092 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PJ | SA611PJ | sa61 1pj | sa611pj | Pembrokeshire | Sir Benfro | Keeston WwTW | 5353 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194890 | 215206 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PL | SA611PL | sa61 1pl | sa611pl | Pembrokeshire | Sir Benfro | Keeston WwTW | 5361 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194829 | 215123 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PQ | SA611PQ | sa61 1pq | sa611pq | Pembrokeshire | Sir Benfro | Keeston WwTW | 5502 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194964 | 215064 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PR | SA611PR | sa61 1pr | sa611pr | Pembrokeshire | Sir Benfro | Camrose WwTW | 5333 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195391 | 215558 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PS | SA611PS | sa61 1ps | sa611ps | Pembrokeshire | Sir Benfro | Camrose WwTW | 5352 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195408 | 215546 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PT | SA611PT | sa61 1pt | sa611pt | Pembrokeshire | Sir Benfro | Camrose WwTW | 5431 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195414 | 215456 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PU | SA611PU | sa61 1pu | sa611pu | Pembrokeshire | Sir Benfro | Camrose WwTW | 5630 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195518 | 215287 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PW | SA611PW | sa61 1pw | sa611pw | Pembrokeshire | Sir Benfro | Camrose WwTW | 5630 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195518 | 215287 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PX | SA611PX | sa61 1px | sa611px | Pembrokeshire | Sir Benfro | Camrose WwTW | 5370 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195328 | 215474 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1PZ | SA611PZ | sa61 1pz | sa611pz | Pembrokeshire | Sir Benfro | Camrose WwTW | 5585 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195424 | 215281 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QA | SA611QA | sa61 1qa | sa611qa | Pembrokeshire | Sir Benfro | Camrose WwTW | 5397 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195289 | 215419 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QB | SA611QB | sa61 1qb | sa611qb | Pembrokeshire | Sir Benfro | Camrose WwTW | 5447 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195328 | 215384 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QD | SA611QD | sa61 1qd | sa611qd | Pembrokeshire | Sir Benfro | Camrose WwTW | 5430 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195278 | 215374 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QE | SA611QE | sa61 1qe | sa611qe | Pembrokeshire | Sir Benfro | Camrose WwTW | 5465 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195221 | 215300 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QF | SA611QF | sa61 1qf | sa611qf | Pembrokeshire | Sir Benfro | Camrose WwTW | 5407 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195228 | 215371 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QH | SA611QH | sa61 1qh | sa611qh | Pembrokeshire | Sir Benfro | Camrose WwTW | 5378 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195199 | 215388 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QJ | SA611QJ | sa61 1qj | sa611qj | Pembrokeshire | Sir Benfro | Camrose WwTW | 5405 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195180 | 215345 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QL | SA611QL | sa61 1ql | sa611ql | Pembrokeshire | Sir Benfro | Camrose WwTW | 5462 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195188 | 215284 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QN | SA611QN | sa61 1qn | sa611qn | Pembrokeshire | Sir Benfro | Camrose WwTW | 5539 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195112 | 215155 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QP | SA611QP | sa61 1qp | sa611qp | Pembrokeshire | Sir Benfro | Camrose WwTW | 5454 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195142 | 215268 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QQ | SA611QQ | sa61 1qq | sa611qq | Pembrokeshire | Sir Benfro | Camrose WwTW | 5355 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195213 | 215422 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QR | SA611QR | sa61 1qr | sa611qr | Pembrokeshire | Sir Benfro | Camrose WwTW | 5430 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195248 | 215356 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QS | SA611QS | sa61 1qs | sa611qs | Pembrokeshire | Sir Benfro | Camrose WwTW | 5536 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195157 | 215183 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QT | SA611QT | sa61 1qt | sa611qt | Pembrokeshire | Sir Benfro | Camrose WwTW | 5536 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195205 | 215209 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QU | SA611QU | sa61 1qu | sa611qu | Pembrokeshire | Sir Benfro | Camrose WwTW | 5536 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195232 | 215224 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QW | SA611QW | sa61 1qw | sa611qw | Pembrokeshire | Sir Benfro | Camrose WwTW | 5474 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195110 | 215228 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1QX | SA611QX | sa61 1qx | sa611qx | Pembrokeshire | Sir Benfro | Camrose WwTW | 5545 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195272 | 215237 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RH | SA611RH | sa61 1rh | sa611rh | Pembrokeshire | Sir Benfro | Camrose WwTW | 5481 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195230 | 215287 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RJ | SA611RJ | sa61 1rj | sa611rj | Pembrokeshire | Sir Benfro | Camrose WwTW | 5478 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195316 | 215341 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RN | SA611RN | sa61 1rn | sa611rn | Pembrokeshire | Sir Benfro | Camrose WwTW | 5657 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195429 | 215199 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RP | SA611RP | sa61 1rp | sa611rp | Pembrokeshire | Sir Benfro | Camrose WwTW | 5629 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195320 | 215167 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RR | SA611RR | sa61 1rr | sa611rr | Pembrokeshire | Sir Benfro | Camrose WwTW | 5721 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195408 | 215112 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RS | SA611RS | sa61 1rs | sa611rs | Pembrokeshire | Sir Benfro | Camrose WwTW | 5733 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195371 | 215077 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RT | SA611RT | sa61 1rt | sa611rt | Pembrokeshire | Sir Benfro | Camrose WwTW | 5728 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195477 | 215145 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RU | SA611RU | sa61 1ru | sa611ru | Pembrokeshire | Sir Benfro | Camrose WwTW | 5886 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195462 | 214953 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RW | SA611RW | sa61 1rw | sa611rw | Pembrokeshire | Sir Benfro | Camrose WwTW | 5663 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195348 | 215145 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1RZ | SA611RZ | sa61 1rz | sa611rz | Pembrokeshire | Sir Benfro | Camrose WwTW | 5874 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195610 | 215056 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SA | SA611SA | sa61 1sa | sa611sa | Pembrokeshire | Sir Benfro | Camrose WwTW | 5766 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195461 | 215092 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SB | SA611SB | sa61 1sb | sa611sb | Pembrokeshire | Sir Benfro | Camrose WwTW | 5587 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195372 | 215247 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SD | SA611SD | sa61 1sd | sa611sd | Pembrokeshire | Sir Benfro | Camrose WwTW | 5712 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195333 | 215079 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SE | SA611SE | sa61 1se | sa611se | Pembrokeshire | Sir Benfro | Camrose WwTW | 5784 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195382 | 215024 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SF | SA611SF | sa61 1sf | sa611sf | Pembrokeshire | Sir Benfro | Camrose WwTW | 5730 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195220 | 214996 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SH | SA611SH | sa61 1sh | sa611sh | Pembrokeshire | Sir Benfro | Camrose WwTW | 5785 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195264 | 214957 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SJ | SA611SJ | sa61 1sj | sa611sj | Pembrokeshire | Sir Benfro | Keeston WwTW | 5692 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195146 | 214983 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SL | SA611SL | sa61 1sl | sa611sl | Pembrokeshire | Sir Benfro | Camrose WwTW | 5854 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195565 | 215052 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SP | SA611SP | sa61 1sp | sa611sp | Pembrokeshire | Sir Benfro | Camrose WwTW | 5175 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195173 | 215608 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SQ | SA611SQ | sa61 1sq | sa611sq | Pembrokeshire | Sir Benfro | Camrose WwTW | 5811 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195264 | 214928 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SR | SA611SR | sa61 1sr | sa611sr | Pembrokeshire | Sir Benfro | Camrose WwTW | 5202 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195163 | 215571 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1ST | SA611ST | sa61 1st | sa611st | Pembrokeshire | Sir Benfro | Camrose WwTW | 5329 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195101 | 215388 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SW | SA611SW | sa61 1sw | sa611sw | Pembrokeshire | Sir Benfro | Camrose WwTW | 5953 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195697 | 215017 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SX | SA611SX | sa61 1sx | sa611sx | Pembrokeshire | Sir Benfro | Camrose WwTW | 5293 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194959 | 215352 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1SY | SA611SY | sa61 1sy | sa611sy | Pembrokeshire | Sir Benfro | Camrose WwTW | 5381 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194986 | 215267 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TA | SA611TA | sa61 1ta | sa611ta | Pembrokeshire | Sir Benfro | Keeston WwTW | 5311 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194909 | 215294 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TB | SA611TB | sa61 1tb | sa611tb | Pembrokeshire | Sir Benfro | Keeston WwTW | 5323 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194905 | 215270 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TD | SA611TD | sa61 1td | sa611td | Pembrokeshire | Sir Benfro | Camrose WwTW | 5201 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194957 | 215455 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TE | SA611TE | sa61 1te | sa611te | Pembrokeshire | Sir Benfro | Camrose WwTW | 5665 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195396 | 215170 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TF | SA611TF | sa61 1tf | sa611tf | Pembrokeshire | Sir Benfro | Keeston WwTW | 5279 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194905 | 215340 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TG | SA611TG | sa61 1tg | sa611tg | Pembrokeshire | Sir Benfro | Camrose WwTW | 5206 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194995 | 215470 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TH | SA611TH | sa61 1th | sa611th | Pembrokeshire | Sir Benfro | Camrose WwTW | 5447 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195255 | 215340 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TN | SA611TN | sa61 1tn | sa611tn | Pembrokeshire | Sir Benfro | Camrose WwTW | 5507 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195701 | 215558 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TP | SA611TP | sa61 1tp | sa611tp | Pembrokeshire | Sir Benfro | Camrose WwTW | 5389 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195570 | 215610 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TQ | SA611TQ | sa61 1tq | sa611tq | Pembrokeshire | Sir Benfro | Camrose WwTW | 5316 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 194949 | 215321 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TR | SA611TR | sa61 1tr | sa611tr | Pembrokeshire | Sir Benfro | Camrose WwTW | 5619 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195726 | 215438 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TS | SA611TS | sa61 1ts | sa611ts | Pembrokeshire | Sir Benfro | Camrose WwTW | 5555 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195734 | 215522 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TT | SA611TT | sa61 1tt | sa611tt | Pembrokeshire | Sir Benfro | Camrose WwTW | 5555 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195781 | 215557 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TU | SA611TU | sa61 1tu | sa611tu | Pembrokeshire | Sir Benfro | Camrose WwTW | 5664 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195887 | 215499 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TW | SA611TW | sa61 1tw | sa611tw | Pembrokeshire | Sir Benfro | Camrose WwTW | 5765 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195871 | 215362 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TX | SA611TX | sa61 1tx | sa611tx | Pembrokeshire | Sir Benfro | Camrose WwTW | 5627 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195888 | 215546 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1TY | SA611TY | sa61 1ty | sa611ty | Pembrokeshire | Sir Benfro | Camrose WwTW | 5712 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 196038 | 215555 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UB | SA611UB | sa61 1ub | sa611ub | Pembrokeshire | Sir Benfro | Camrose WwTW | 5755 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195970 | 215448 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UD | SA611UD | sa61 1ud | sa611ud | Pembrokeshire | Sir Benfro | Camrose WwTW | 5827 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 196107 | 215463 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UG | SA611UG | sa61 1ug | sa611ug | Pembrokeshire | Sir Benfro | Camrose WwTW | 5519 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195649 | 215507 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UL | SA611UL | sa61 1ul | sa611ul | Pembrokeshire | Sir Benfro | Camrose WwTW | 5755 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195560 | 215165 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UN | SA611UN | sa61 1un | sa611un | Pembrokeshire | Sir Benfro | Camrose WwTW | 5284 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195025 | 215398 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UR | SA611UR | sa61 1ur | sa611ur | Pembrokeshire | Sir Benfro | Camrose WwTW | 6212 | 1194 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.25 | 11.87 | 13.12 | 196647 | 215414 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1UU | SA611UU | sa61 1uu | sa611uu | Pembrokeshire | Sir Benfro | Camrose WwTW | 5748 | 1175 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.9 | 11.68 | 12.91 | 195516 | 215146 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 1ZA | SA611ZA | sa61 1za | sa611za | Pembrokeshire | Sir Benfro | Camrose WwTW | 5389 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195570 | 215610 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2AA | SA612AA | sa61 2aa | sa612aa | Pembrokeshire | Sir Benfro | Camrose WwTW | 5266 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195418 | 215656 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2AB | SA612AB | sa61 2ab | sa612ab | Pembrokeshire | Sir Benfro | Camrose WwTW | 5261 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195448 | 215682 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2AD | SA612AD | sa61 2ad | sa612ad | Pembrokeshire | Sir Benfro | Camrose WwTW | 5152 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195378 | 215766 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2AH | SA612AH | sa61 2ah | sa612ah | Pembrokeshire | Sir Benfro | Camrose WwTW | 5524 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195810 | 215617 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2AJ | SA612AJ | sa61 2aj | sa612aj | Pembrokeshire | Sir Benfro | Camrose WwTW | 5057 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195342 | 215856 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2AL | SA612AL | sa61 2al | sa612al | Pembrokeshire | Sir Benfro | Camrose WwTW | 5178 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195407 | 215754 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2AN | SA612AN | sa61 2an | sa612an | Pembrokeshire | Sir Benfro | Camrose WwTW | 5058 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195376 | 215878 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2AT | SA612AT | sa61 2at | sa612at | Pembrokeshire | Sir Benfro | Camrose WwTW | 4387 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195817 | 217168 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2AU | SA612AU | sa61 2au | sa612au | Pembrokeshire | Sir Benfro | Keeston WwTW | 4301 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194068 | 215863 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2AX | SA612AX | sa61 2ax | sa612ax | Pembrokeshire | Sir Benfro | Keeston WwTW | 4883 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194587 | 215576 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2AY | SA612AY | sa61 2ay | sa612ay | Pembrokeshire | Sir Benfro | Keeston WwTW | 4490 | 1178 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.96 | 11.71 | 12.94 | 193977 | 215490 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2AZ | SA612AZ | sa61 2az | sa612az | Pembrokeshire | Sir Benfro | Keeston WwTW | 4518 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194065 | 215538 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2BA | SA612BA | sa61 2ba | sa612ba | Pembrokeshire | Sir Benfro | Keeston WwTW | 4377 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 193843 | 215516 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2BB | SA612BB | sa61 2bb | sa612bb | Pembrokeshire | Sir Benfro | Keeston WwTW | 4485 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194047 | 215568 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2BD | SA612BD | sa61 2bd | sa612bd | Pembrokeshire | Sir Benfro | Keeston WwTW | 4600 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194240 | 215606 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2BE | SA612BE | sa61 2be | sa612be | Pembrokeshire | Sir Benfro | Keeston WwTW | 4660 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194292 | 215575 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2BG | SA612BG | sa61 2bg | sa612bg | Pembrokeshire | Sir Benfro | Keeston WwTW | 4667 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194358 | 215639 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2BH | SA612BH | sa61 2bh | sa612bh | Pembrokeshire | Sir Benfro | Camrose WwTW | 5243 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195320 | 215619 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2BJ | SA612BJ | sa61 2bj | sa612bj | Pembrokeshire | Sir Benfro | Camrose WwTW | 4843 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195699 | 216403 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2BN | SA612BN | sa61 2bn | sa612bn | Pembrokeshire | Sir Benfro | Camrose WwTW | 5296 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195426 | 215625 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2BP | SA612BP | sa61 2bp | sa612bp | Pembrokeshire | Sir Benfro | Camrose WwTW | 5293 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195397 | 215610 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2BQ | SA612BQ | sa61 2bq | sa612bq | Pembrokeshire | Sir Benfro | Keeston WwTW | 4883 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194587 | 215576 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2BU | SA612BU | sa61 2bu | sa612bu | Pembrokeshire | Sir Benfro | Camrose WwTW | 5282 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195371 | 215606 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2BW | SA612BW | sa61 2bw | sa612bw | Pembrokeshire | Sir Benfro | Camrose WwTW | 5264 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195293 | 215577 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2DA | SA612DA | sa61 2da | sa612da | Pembrokeshire | Sir Benfro | Camrose WwTW | 5248 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195321 | 215614 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2DB | SA612DB | sa61 2db | sa612db | Pembrokeshire | Sir Benfro | Camrose WwTW | 5220 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195263 | 215610 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2DE | SA612DE | sa61 2de | sa612de | Pembrokeshire | Sir Benfro | Camrose WwTW | 5232 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195289 | 215613 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2DJ | SA612DJ | sa61 2dj | sa612dj | Pembrokeshire | Sir Benfro | Camrose WwTW | 5220 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195231 | 215591 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2DN | SA612DN | sa61 2dn | sa612dn | Pembrokeshire | Sir Benfro | Camrose WwTW | 5659 | 1177 | 900to1200 | 2.36 | 1.72 | 1.26 | 21.94 | 11.7 | 12.93 | 195309 | 215127 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2DR | SA612DR | sa61 2dr | sa612dr | Pembrokeshire | Sir Benfro | Camrose WwTW | 5191 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195201 | 215606 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2DS | SA612DS | sa61 2ds | sa612ds | Pembrokeshire | Sir Benfro | Camrose WwTW | 5181 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195202 | 215619 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2DT | SA612DT | sa61 2dt | sa612dt | Pembrokeshire | Sir Benfro | Camrose WwTW | 5126 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195147 | 215650 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2DU | SA612DU | sa61 2du | sa612du | Pembrokeshire | Sir Benfro | Camrose WwTW | 5144 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195136 | 215622 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2DX | SA612DX | sa61 2dx | sa612dx | Pembrokeshire | Sir Benfro | Camrose WwTW | 5086 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195140 | 215692 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2DY | SA612DY | sa61 2dy | sa612dy | Pembrokeshire | Sir Benfro | Camrose WwTW | 5090 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195162 | 215701 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2DZ | SA612DZ | sa61 2dz | sa612dz | Pembrokeshire | Sir Benfro | Camrose WwTW | 5076 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195122 | 215693 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2EA | SA612EA | sa61 2ea | sa612ea | Pembrokeshire | Sir Benfro | Camrose WwTW | 5104 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195192 | 215703 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2EB | SA612EB | sa61 2eb | sa612eb | Pembrokeshire | Sir Benfro | Camrose WwTW | 5090 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195218 | 215736 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2ED | SA612ED | sa61 2ed | sa612ed | Pembrokeshire | Sir Benfro | Camrose WwTW | 5122 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195238 | 215711 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2EE | SA612EE | sa61 2ee | sa612ee | Pembrokeshire | Sir Benfro | Camrose WwTW | 5121 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195252 | 215720 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2EF | SA612EF | sa61 2ef | sa612ef | Pembrokeshire | Sir Benfro | Camrose WwTW | 5162 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195326 | 215719 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2EG | SA612EG | sa61 2eg | sa612eg | Pembrokeshire | Sir Benfro | Camrose WwTW | 5147 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195252 | 215690 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2EH | SA612EH | sa61 2eh | sa612eh | Pembrokeshire | Sir Benfro | Camrose WwTW | 5046 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195110 | 215721 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2EJ | SA612EJ | sa61 2ej | sa612ej | Pembrokeshire | Sir Benfro | Camrose WwTW | 5081 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195072 | 215657 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2EL | SA612EL | sa61 2el | sa612el | Pembrokeshire | Sir Benfro | Camrose WwTW | 5078 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195068 | 215659 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2ET | SA612ET | sa61 2et | sa612et | Pembrokeshire | Sir Benfro | Camrose WwTW | 5075 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195457 | 215915 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2EW | SA612EW | sa61 2ew | sa612ew | Pembrokeshire | Sir Benfro | Camrose WwTW | 5078 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195254 | 215773 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2EX | SA612EX | sa61 2ex | sa612ex | Pembrokeshire | Sir Benfro | Camrose WwTW | 4827 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195478 | 216240 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2EZ | SA612EZ | sa61 2ez | sa612ez | Pembrokeshire | Sir Benfro | Camrose WwTW | 5093 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195431 | 215874 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2GA | SA612GA | sa61 2ga | sa612ga | Pembrokeshire | Sir Benfro | Camrose WwTW | 4123 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 195041 | 216793 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2GB | SA612GB | sa61 2gb | sa612gb | Pembrokeshire | Sir Benfro | Camrose WwTW | 4035 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 195083 | 216940 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2GD | SA612GD | sa61 2gd | sa612gd | Pembrokeshire | Sir Benfro | Camrose WwTW | 4142 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 195097 | 216812 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2GE | SA612GE | sa61 2ge | sa612ge | Pembrokeshire | Sir Benfro | Camrose WwTW | 3993 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 194957 | 216892 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2GF | SA612GF | sa61 2gf | sa612gf | Pembrokeshire | Sir Benfro | Camrose WwTW | 4157 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 195083 | 216782 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2GG | SA612GG | sa61 2gg | sa612gg | Pembrokeshire | Sir Benfro | Camrose WwTW | 4235 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 195178 | 216758 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2GH | SA612GH | sa61 2gh | sa612gh | Pembrokeshire | Sir Benfro | Camrose WwTW | 4111 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 194994 | 216771 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HA | SA612HA | sa61 2ha | sa612ha | Pembrokeshire | Sir Benfro | Camrose WwTW | 4284 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 195097 | 216632 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HD | SA612HD | sa61 2hd | sa612hd | Pembrokeshire | Sir Benfro | Camrose WwTW | 4978 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195274 | 215906 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HE | SA612HE | sa61 2he | sa612he | Pembrokeshire | Sir Benfro | Camrose WwTW | 4973 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195196 | 215861 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HF | SA612HF | sa61 2hf | sa612hf | Pembrokeshire | Sir Benfro | Camrose WwTW | 4676 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195053 | 216122 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HH | SA612HH | sa61 2hh | sa612hh | Pembrokeshire | Sir Benfro | Camrose WwTW | 4498 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194973 | 216282 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HL | SA612HL | sa61 2hl | sa612hl | Pembrokeshire | Sir Benfro | Camrose WwTW | 4683 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195202 | 216215 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HN | SA612HN | sa61 2hn | sa612hn | Pembrokeshire | Sir Benfro | Camrose WwTW | 4894 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195247 | 215989 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HP | SA612HP | sa61 2hp | sa612hp | Pembrokeshire | Sir Benfro | Camrose WwTW | 4407 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195123 | 216498 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HQ | SA612HQ | sa61 2hq | sa612hq | Pembrokeshire | Sir Benfro | Camrose WwTW | 4557 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195104 | 216299 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HR | SA612HR | sa61 2hr | sa612hr | Pembrokeshire | Sir Benfro | Camrose WwTW | 4474 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195142 | 216429 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HS | SA612HS | sa61 2hs | sa612hs | Pembrokeshire | Sir Benfro | Camrose WwTW | 4406 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194966 | 216388 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HT | SA612HT | sa61 2ht | sa612ht | Pembrokeshire | Sir Benfro | Camrose WwTW | 4432 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195037 | 216405 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HX | SA612HX | sa61 2hx | sa612hx | Pembrokeshire | Sir Benfro | Camrose WwTW | 4673 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195153 | 216192 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HY | SA612HY | sa61 2hy | sa612hy | Pembrokeshire | Sir Benfro | Camrose WwTW | 4613 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195078 | 216214 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2HZ | SA612HZ | sa61 2hz | sa612hz | Pembrokeshire | Sir Benfro | Camrose WwTW | 4877 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195189 | 215970 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JA | SA612JA | sa61 2ja | sa612ja | Pembrokeshire | Sir Benfro | Camrose WwTW | 4805 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195194 | 216061 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JD | SA612JD | sa61 2jd | sa612jd | Pembrokeshire | Sir Benfro | Camrose WwTW | 5048 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195181 | 215762 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JE | SA612JE | sa61 2je | sa612je | Pembrokeshire | Sir Benfro | Camrose WwTW | 4983 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195211 | 215858 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JF | SA612JF | sa61 2jf | sa612jf | Pembrokeshire | Sir Benfro | Camrose WwTW | 4994 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195230 | 215857 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JG | SA612JG | sa61 2jg | sa612jg | Pembrokeshire | Sir Benfro | Camrose WwTW | 5070 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195210 | 215754 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JH | SA612JH | sa61 2jh | sa612jh | Pembrokeshire | Sir Benfro | Camrose WwTW | 5048 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195214 | 215783 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JJ | SA612JJ | sa61 2jj | sa612jj | Pembrokeshire | Sir Benfro | Camrose WwTW | 5035 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195265 | 215831 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JL | SA612JL | sa61 2jl | sa612jl | Pembrokeshire | Sir Benfro | Camrose WwTW | 5025 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195269 | 215846 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JN | SA612JN | sa61 2jn | sa612jn | Pembrokeshire | Sir Benfro | Camrose WwTW | 5006 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195276 | 215873 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JP | SA612JP | sa61 2jp | sa612jp | Pembrokeshire | Sir Benfro | Camrose WwTW | 5019 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195307 | 215878 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JQ | SA612JQ | sa61 2jq | sa612jq | Pembrokeshire | Sir Benfro | Camrose WwTW | 5022 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195219 | 215817 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JR | SA612JR | sa61 2jr | sa612jr | Pembrokeshire | Sir Benfro | Camrose WwTW | 4292 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 194970 | 216529 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2JX | SA612JX | sa61 2jx | sa612jx | Pembrokeshire | Sir Benfro | Camrose WwTW | 5301 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195476 | 215653 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2LE | SA612LE | sa61 2le | sa612le | Pembrokeshire | Sir Benfro | Camrose WwTW | 5318 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195570 | 215697 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2LG | SA612LG | sa61 2lg | sa612lg | Pembrokeshire | Sir Benfro | Camrose WwTW | 5333 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195663 | 215745 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2LH | SA612LH | sa61 2lh | sa612lh | Pembrokeshire | Sir Benfro | Camrose WwTW | 5505 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195866 | 215683 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2LJ | SA612LJ | sa61 2lj | sa612lj | Pembrokeshire | Sir Benfro | Camrose WwTW | 5149 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195479 | 215839 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2LP | SA612LP | sa61 2lp | sa612lp | Pembrokeshire | Sir Benfro | Camrose WwTW | 5277 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195465 | 215674 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2LQ | SA612LQ | sa61 2lq | sa612lq | Pembrokeshire | Sir Benfro | Camrose WwTW | 5278 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195472 | 215677 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2LR | SA612LR | sa61 2lr | sa612lr | Pembrokeshire | Sir Benfro | Camrose WwTW | 5280 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195486 | 215685 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2LU | SA612LU | sa61 2lu | sa612lu | Pembrokeshire | Sir Benfro | Camrose WwTW | 5290 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195539 | 215709 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2LX | SA612LX | sa61 2lx | sa612lx | Pembrokeshire | Sir Benfro | Camrose WwTW | 5288 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195569 | 215733 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2LZ | SA612LZ | sa61 2lz | sa612lz | Pembrokeshire | Sir Benfro | Camrose WwTW | 5544 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195890 | 215653 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2NB | SA612NB | sa61 2nb | sa612nb | Pembrokeshire | Sir Benfro | Camrose WwTW | 5295 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195597 | 215744 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2ND | SA612ND | sa61 2nd | sa612nd | Pembrokeshire | Sir Benfro | Camrose WwTW | 5114 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195553 | 215936 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2NE | SA612NE | sa61 2ne | sa612ne | Pembrokeshire | Sir Benfro | Camrose WwTW | 5166 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195581 | 215893 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2NF | SA612NF | sa61 2nf | sa612nf | Pembrokeshire | Sir Benfro | Camrose WwTW | 5233 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195613 | 215833 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2NL | SA612NL | sa61 2nl | sa612nl | Pembrokeshire | Sir Benfro | Camrose WwTW | 5313 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195671 | 215776 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2NT | SA612NT | sa61 2nt | sa612nt | Pembrokeshire | Sir Benfro | Camrose WwTW | 5322 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195748 | 215823 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2NU | SA612NU | sa61 2nu | sa612nu | Pembrokeshire | Sir Benfro | Camrose WwTW | 5294 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195797 | 215897 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2NX | SA612NX | sa61 2nx | sa612nx | Pembrokeshire | Sir Benfro | Camrose WwTW | 5283 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195894 | 215991 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2NZ | SA612NZ | sa61 2nz | sa612nz | Pembrokeshire | Sir Benfro | Camrose WwTW | 5170 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195641 | 215933 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PA | SA612PA | sa61 2pa | sa612pa | Pembrokeshire | Sir Benfro | Camrose WwTW | 5218 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195686 | 215907 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PB | SA612PB | sa61 2pb | sa612pb | Pembrokeshire | Sir Benfro | Camrose WwTW | 5111 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195671 | 216031 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PD | SA612PD | sa61 2pd | sa612pd | Pembrokeshire | Sir Benfro | Camrose WwTW | 5119 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195617 | 215978 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PE | SA612PE | sa61 2pe | sa612pe | Pembrokeshire | Sir Benfro | Camrose WwTW | 5002 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195687 | 216184 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PF | SA612PF | sa61 2pf | sa612pf | Pembrokeshire | Sir Benfro | Camrose WwTW | 4917 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195774 | 216371 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PG | SA612PG | sa61 2pg | sa612pg | Pembrokeshire | Sir Benfro | Camrose WwTW | 4671 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195982 | 216926 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PH | SA612PH | sa61 2ph | sa612ph | Pembrokeshire | Sir Benfro | Camrose WwTW | 4900 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195756 | 216377 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PJ | SA612PJ | sa61 2pj | sa612pj | Pembrokeshire | Sir Benfro | Camrose WwTW | 4911 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195727 | 216337 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PL | SA612PL | sa61 2pl | sa612pl | Pembrokeshire | Sir Benfro | Camrose WwTW | 4631 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195586 | 216586 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PN | SA612PN | sa61 2pn | sa612pn | Pembrokeshire | Sir Benfro | Camrose WwTW | 4937 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195642 | 216231 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PP | SA612PP | sa61 2pp | sa612pp | Pembrokeshire | Sir Benfro | Camrose WwTW | 5002 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195641 | 216146 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PQ | SA612PQ | sa61 2pq | sa612pq | Pembrokeshire | Sir Benfro | Camrose WwTW | 4864 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195763 | 216432 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PS | SA612PS | sa61 2ps | sa612ps | Pembrokeshire | Sir Benfro | Camrose WwTW | 4646 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196121 | 217128 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PT | SA612PT | sa61 2pt | sa612pt | Pembrokeshire | Sir Benfro | Camrose WwTW | 4526 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196035 | 217213 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PU | SA612PU | sa61 2pu | sa612pu | Pembrokeshire | Sir Benfro | Camrose WwTW | 4813 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195798 | 216534 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PW | SA612PW | sa61 2pw | sa612pw | Pembrokeshire | Sir Benfro | Camrose WwTW | 5087 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195574 | 215986 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PX | SA612PX | sa61 2px | sa612px | Pembrokeshire | Sir Benfro | Camrose WwTW | 4817 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195835 | 216564 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PY | SA612PY | sa61 2py | sa612py | Pembrokeshire | Sir Benfro | Camrose WwTW | 4678 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195787 | 216710 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2PZ | SA612PZ | sa61 2pz | sa612pz | Pembrokeshire | Sir Benfro | Camrose WwTW | 4526 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195698 | 216836 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QA | SA612QA | sa61 2qa | sa612qa | Pembrokeshire | Sir Benfro | Camrose WwTW | 4721 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195890 | 216754 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QB | SA612QB | sa61 2qb | sa612qb | Pembrokeshire | Sir Benfro | Camrose WwTW | 4572 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195970 | 217062 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QE | SA612QE | sa61 2qe | sa612qe | Pembrokeshire | Sir Benfro | Camrose WwTW | 4687 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195965 | 216883 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QF | SA612QF | sa61 2qf | sa612qf | Pembrokeshire | Sir Benfro | Camrose WwTW | 4672 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196091 | 217050 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QG | SA612QG | sa61 2qg | sa612qg | Pembrokeshire | Sir Benfro | Camrose WwTW | 4854 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195871 | 216547 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QH | SA612QH | sa61 2qh | sa612qh | Pembrokeshire | Sir Benfro | Camrose WwTW | 4792 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195902 | 216665 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QJ | SA612QJ | sa61 2qj | sa612qj | Pembrokeshire | Sir Benfro | Camrose WwTW | 4914 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196025 | 216615 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QL | SA612QL | sa61 2ql | sa612ql | Pembrokeshire | Sir Benfro | Camrose WwTW | 4730 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195937 | 216790 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QN | SA612QN | sa61 2qn | sa612qn | Pembrokeshire | Sir Benfro | Camrose WwTW | 4832 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195996 | 216704 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QP | SA612QP | sa61 2qp | sa612qp | Pembrokeshire | Sir Benfro | Camrose WwTW | 4877 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196118 | 216769 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QQ | SA612QQ | sa61 2qq | sa612qq | Pembrokeshire | Sir Benfro | Camrose WwTW | 4878 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195908 | 216549 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QR | SA612QR | sa61 2qr | sa612qr | Pembrokeshire | Sir Benfro | Camrose WwTW | 4738 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196191 | 217069 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QS | SA612QS | sa61 2qs | sa612qs | Pembrokeshire | Sir Benfro | Camrose WwTW | 4780 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196162 | 216967 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QU | SA612QU | sa61 2qu | sa612qu | Pembrokeshire | Sir Benfro | Camrose WwTW | 4925 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195897 | 216473 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QW | SA612QW | sa61 2qw | sa612qw | Pembrokeshire | Sir Benfro | Camrose WwTW | 4762 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196004 | 216815 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QX | SA612QX | sa61 2qx | sa612qx | Pembrokeshire | Sir Benfro | Camrose WwTW | 4939 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195838 | 216399 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QY | SA612QY | sa61 2qy | sa612qy | Pembrokeshire | Sir Benfro | Camrose WwTW | 4978 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195768 | 216284 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2QZ | SA612QZ | sa61 2qz | sa612qz | Pembrokeshire | Sir Benfro | Camrose WwTW | 4766 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195758 | 216561 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RA | SA612RA | sa61 2ra | sa612ra | Pembrokeshire | Sir Benfro | Camrose WwTW | 4994 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195886 | 216369 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RB | SA612RB | sa61 2rb | sa612rb | Pembrokeshire | Sir Benfro | Camrose WwTW | 5022 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195958 | 216397 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RD | SA612RD | sa61 2rd | sa612rd | Pembrokeshire | Sir Benfro | Camrose WwTW | 5135 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195984 | 216267 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RE | SA612RE | sa61 2re | sa612re | Pembrokeshire | Sir Benfro | Camrose WwTW | 5079 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195899 | 216265 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RF | SA612RF | sa61 2rf | sa612rf | Pembrokeshire | Sir Benfro | Camrose WwTW | 4872 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196259 | 216939 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RG | SA612RG | sa61 2rg | sa612rg | Pembrokeshire | Sir Benfro | Camrose WwTW | 5128 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195875 | 216178 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RH | SA612RH | sa61 2rh | sa612rh | Pembrokeshire | Sir Benfro | Camrose WwTW | 4911 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196298 | 216925 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RJ | SA612RJ | sa61 2rj | sa612rj | Pembrokeshire | Sir Benfro | Camrose WwTW | 4824 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196166 | 216904 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RL | SA612RL | sa61 2rl | sa612rl | Pembrokeshire | Sir Benfro | Camrose WwTW | 4903 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194770 | 215693 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RN | SA612RN | sa61 2rn | sa612rn | Pembrokeshire | Sir Benfro | Keeston WwTW | 4823 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194603 | 215692 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RP | SA612RP | sa61 2rp | sa612rp | Pembrokeshire | Sir Benfro | Camrose WwTW | 4842 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194661 | 215706 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RQ | SA612RQ | sa61 2rq | sa612rq | Pembrokeshire | Sir Benfro | Camrose WwTW | 5097 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195880 | 216224 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RR | SA612RR | sa61 2rr | sa612rr | Pembrokeshire | Sir Benfro | Camrose WwTW | 4872 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194802 | 215745 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RS | SA612RS | sa61 2rs | sa612rs | Pembrokeshire | Sir Benfro | Camrose WwTW | 4808 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194888 | 215866 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RT | SA612RT | sa61 2rt | sa612rt | Pembrokeshire | Sir Benfro | Camrose WwTW | 4752 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194856 | 215913 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RU | SA612RU | sa61 2ru | sa612ru | Pembrokeshire | Sir Benfro | Camrose WwTW | 4769 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194807 | 215865 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RX | SA612RX | sa61 2rx | sa612rx | Pembrokeshire | Sir Benfro | Camrose WwTW | 4776 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194698 | 215799 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2RY | SA612RY | sa61 2ry | sa612ry | Pembrokeshire | Sir Benfro | Camrose WwTW | 4700 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194646 | 215858 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SA | SA612SA | sa61 2sa | sa612sa | Pembrokeshire | Sir Benfro | Camrose WwTW | 4675 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194801 | 215970 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SB | SA612SB | sa61 2sb | sa612sb | Pembrokeshire | Sir Benfro | Camrose WwTW | 4683 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194689 | 215899 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SD | SA612SD | sa61 2sd | sa612sd | Pembrokeshire | Sir Benfro | Camrose WwTW | 4632 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194641 | 215932 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SE | SA612SE | sa61 2se | sa612se | Pembrokeshire | Sir Benfro | Camrose WwTW | 4584 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194517 | 215923 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SF | SA612SF | sa61 2sf | sa612sf | Pembrokeshire | Sir Benfro | Camrose WwTW | 4994 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194829 | 215622 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SG | SA612SG | sa61 2sg | sa612sg | Pembrokeshire | Sir Benfro | Camrose WwTW | 4492 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194437 | 215987 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SH | SA612SH | sa61 2sh | sa612sh | Pembrokeshire | Sir Benfro | Camrose WwTW | 4653 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194840 | 216018 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SJ | SA612SJ | sa61 2sj | sa612sj | Pembrokeshire | Sir Benfro | Camrose WwTW | 4700 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194877 | 215985 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SL | SA612SL | sa61 2sl | sa612sl | Pembrokeshire | Sir Benfro | Camrose WwTW | 4797 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194991 | 215940 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SN | SA612SN | sa61 2sn | sa612sn | Pembrokeshire | Sir Benfro | Camrose WwTW | 4773 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194929 | 215931 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SP | SA612SP | sa61 2sp | sa612sp | Pembrokeshire | Sir Benfro | Camrose WwTW | 4819 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195024 | 215934 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SQ | SA612SQ | sa61 2sq | sa612sq | Pembrokeshire | Sir Benfro | Camrose WwTW | 4583 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194616 | 215974 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SS | SA612SS | sa61 2ss | sa612ss | Pembrokeshire | Sir Benfro | Camrose WwTW | 4827 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194943 | 215876 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2ST | SA612ST | sa61 2st | sa612st | Pembrokeshire | Sir Benfro | Camrose WwTW | 4939 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 195008 | 215785 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2SX | SA612SX | sa61 2sx | sa612sx | Pembrokeshire | Sir Benfro | Camrose WwTW | 4858 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195831 | 216503 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TA | SA612TA | sa61 2ta | sa612ta | Pembrokeshire | Sir Benfro | Keeston WwTW | 4268 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 193854 | 215681 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TB | SA612TB | sa61 2tb | sa612tb | Pembrokeshire | Sir Benfro | Keeston WwTW | 4323 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 193942 | 215692 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TD | SA612TD | sa61 2td | sa612td | Pembrokeshire | Sir Benfro | Keeston WwTW | 4249 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 193904 | 215760 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TE | SA612TE | sa61 2te | sa612te | Pembrokeshire | Sir Benfro | Keeston WwTW | 4210 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 193898 | 215810 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TF | SA612TF | sa61 2tf | sa612tf | Pembrokeshire | Sir Benfro | Keeston WwTW | 4322 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 193760 | 215514 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TG | SA612TG | sa61 2tg | sa612tg | Pembrokeshire | Sir Benfro | Keeston WwTW | 4318 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194038 | 215803 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TH | SA612TH | sa61 2th | sa612th | Pembrokeshire | Sir Benfro | Keeston WwTW | 4346 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194051 | 215776 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TJ | SA612TJ | sa61 2tj | sa612tj | Pembrokeshire | Sir Benfro | Keeston WwTW | 4424 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194034 | 215643 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TL | SA612TL | sa61 2tl | sa612tl | Pembrokeshire | Sir Benfro | Keeston WwTW | 4444 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194036 | 215615 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TN | SA612TN | sa61 2tn | sa612tn | Pembrokeshire | Sir Benfro | Keeston WwTW | 4509 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194177 | 215673 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TP | SA612TP | sa61 2tp | sa612tp | Pembrokeshire | Sir Benfro | Keeston WwTW | 4448 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194144 | 215727 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TQ | SA612TQ | sa61 2tq | sa612tq | Pembrokeshire | Sir Benfro | Keeston WwTW | 4274 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 193788 | 215607 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TR | SA612TR | sa61 2tr | sa612tr | Pembrokeshire | Sir Benfro | Keeston WwTW | 4577 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194330 | 215745 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TS | SA612TS | sa61 2ts | sa612ts | Pembrokeshire | Sir Benfro | Keeston WwTW | 4610 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194338 | 215704 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TT | SA612TT | sa61 2tt | sa612tt | Pembrokeshire | Sir Benfro | Keeston WwTW | 4482 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194231 | 215776 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TU | SA612TU | sa61 2tu | sa612tu | Pembrokeshire | Sir Benfro | Keeston WwTW | 4464 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194256 | 215833 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TW | SA612TW | sa61 2tw | sa612tw | Pembrokeshire | Sir Benfro | Keeston WwTW | 4566 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194228 | 215644 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TX | SA612TX | sa61 2tx | sa612tx | Pembrokeshire | Sir Benfro | Keeston WwTW | 4396 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194135 | 215795 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TY | SA612TY | sa61 2ty | sa612ty | Pembrokeshire | Sir Benfro | Keeston WwTW | 4532 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194360 | 215853 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2TZ | SA612TZ | sa61 2tz | sa612tz | Pembrokeshire | Sir Benfro | Keeston WwTW | 4449 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194280 | 215887 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UA | SA612UA | sa61 2ua | sa612ua | Pembrokeshire | Sir Benfro | Keeston WwTW | 4395 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194156 | 215821 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UB | SA612UB | sa61 2ub | sa612ub | Pembrokeshire | Sir Benfro | Keeston WwTW | 4489 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194366 | 215931 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UD | SA612UD | sa61 2ud | sa612ud | Pembrokeshire | Sir Benfro | Keeston WwTW | 4537 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194327 | 215805 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UE | SA612UE | sa61 2ue | sa612ue | Pembrokeshire | Sir Benfro | Keeston WwTW | 4651 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194466 | 215796 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UF | SA612UF | sa61 2uf | sa612uf | Pembrokeshire | Sir Benfro | Keeston WwTW | 4169 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 193606 | 215580 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UG | SA612UG | sa61 2ug | sa612ug | Pembrokeshire | Sir Benfro | Camrose WwTW | 4652 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 194511 | 215845 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UH | SA612UH | sa61 2uh | sa612uh | Pembrokeshire | Sir Benfro | Keeston WwTW | 4524 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 194412 | 215934 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UN | SA612UN | sa61 2un | sa612un | Pembrokeshire | Sir Benfro | Camrose WwTW | 3792 | 1156 | 900to1200 | 2.31 | 1.69 | 1.24 | 21.55 | 11.49 | 12.7 | 195058 | 217240 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UR | SA612UR | sa61 2ur | sa612ur | Pembrokeshire | Sir Benfro | Camrose WwTW | 3768 | 1163 | 900to1200 | 2.33 | 1.7 | 1.25 | 21.68 | 11.56 | 12.78 | 194040 | 216601 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UX | SA612UX | sa61 2ux | sa612ux | Pembrokeshire | Sir Benfro | Keeston WwTW | 3890 | 1157 | 900to1200 | 2.32 | 1.69 | 1.24 | 21.56 | 11.5 | 12.71 | 193685 | 216051 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UY | SA612UY | sa61 2uy | sa612uy | Pembrokeshire | Sir Benfro | Keeston WwTW | 3919 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 193139 | 215522 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2UZ | SA612UZ | sa61 2uz | sa612uz | Pembrokeshire | Sir Benfro | Keeston WwTW | 3756 | 1173 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.86 | 11.66 | 12.89 | 192785 | 215479 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2XE | SA612XE | sa61 2xe | sa612xe | Pembrokeshire | Sir Benfro | Camrose WwTW | 5566 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 196156 | 215842 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2XF | SA612XF | sa61 2xf | sa612xf | Pembrokeshire | Sir Benfro | Camrose WwTW | 5569 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 196393 | 216057 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2XG | SA612XG | sa61 2xg | sa612xg | Pembrokeshire | Sir Benfro | Camrose WwTW | 5762 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 196550 | 215940 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2XH | SA612XH | sa61 2xh | sa612xh | Pembrokeshire | Sir Benfro | Camrose WwTW | 5622 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 196169 | 215779 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2XN | SA612XN | sa61 2xn | sa612xn | Pembrokeshire | Sir Benfro | Camrose WwTW | 5013 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196295 | 216764 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 2XQ | SA612XQ | sa61 2xq | sa612xq | Pembrokeshire | Sir Benfro | Wiston STW | 5575 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 197302 | 216034 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 9SA | SA619SA | sa61 9sa | sa619sa | Pembrokeshire | Sir Benfro | Camrose WwTW | 5389 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195570 | 215610 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA61 9SB | SA619SB | sa61 9sb | sa619sb | Pembrokeshire | Sir Benfro | Camrose WwTW | 5389 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 195570 | 215610 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3GB | SA623GB | sa62 3gb | sa623gb | Pembrokeshire | Sir Benfro | Keeston WwTW | 3993 | 1146 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.36 | 11.39 | 12.59 | 189134 | 215055 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3HS | SA623HS | sa62 3hs | sa623hs | Pembrokeshire | Sir Benfro | Keeston WwTW | 3411 | 1168 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.77 | 11.61 | 12.83 | 190058 | 215352 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LE | SA623LE | sa62 3le | sa623le | Pembrokeshire | Sir Benfro | Keeston WwTW | 3787 | 1134 | 900to1200 | 2.27 | 1.66 | 1.22 | 21.14 | 11.27 | 12.46 | 188187 | 215951 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LF | SA623LF | sa62 3lf | sa623lf | Pembrokeshire | Sir Benfro | Keeston WwTW | 3187 | 1140 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.25 | 11.33 | 12.53 | 188575 | 216411 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LG | SA623LG | sa62 3lg | sa623lg | Pembrokeshire | Sir Benfro | Keeston WwTW | 2270 | 1167 | 900to1200 | 2.34 | 1.71 | 1.25 | 21.75 | 11.6 | 12.82 | 189944 | 216581 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LH | SA623LH | sa62 3lh | sa623lh | Pembrokeshire | Sir Benfro | Keeston WwTW | 3159 | 1145 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.34 | 11.38 | 12.58 | 188503 | 216525 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LL | SA623LL | sa62 3ll | sa623ll | Pembrokeshire | Sir Benfro | Keeston WwTW | 3439 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 191907 | 215416 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LN | SA623LN | sa62 3ln | sa623ln | Pembrokeshire | Sir Benfro | Keeston WwTW | 2374 | 1180 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.99 | 11.73 | 12.96 | 191615 | 216443 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LP | SA623LP | sa62 3lp | sa623lp | Pembrokeshire | Sir Benfro | Keeston WwTW | 2757 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 191046 | 215930 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LQ | SA623LQ | sa62 3lq | sa623lq | Pembrokeshire | Sir Benfro | Keeston WwTW | 2804 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 190523 | 215889 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LR | SA623LR | sa62 3lr | sa623lr | Pembrokeshire | Sir Benfro | Keeston WwTW | 1736 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 190708 | 216945 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LS | SA623LS | sa62 3ls | sa623ls | Pembrokeshire | Sir Benfro | Keeston WwTW | 3403 | 1172 | 900to1200 | 2.35 | 1.72 | 1.26 | 21.84 | 11.65 | 12.88 | 191624 | 215372 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3LU | SA623LU | sa62 3lu | sa623lu | Pembrokeshire | Sir Benfro | Keeston WwTW | 3906 | 1146 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.36 | 11.39 | 12.59 | 189140 | 215149 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3NP | SA623NP | sa62 3np | sa623np | Pembrokeshire | Sir Benfro | Keeston WwTW | 2672 | 1145 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.34 | 11.38 | 12.58 | 188627 | 217143 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 3NR | SA623NR | sa62 3nr | sa623nr | Pembrokeshire | Sir Benfro | Keeston WwTW | 2310 | 1145 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.34 | 11.38 | 12.58 | 189129 | 217099 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4AF | SA624AF | sa62 4af | sa624af | Pembrokeshire | Sir Benfro | Camrose WwTW | 4573 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196125 | 217251 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BB | SA624BB | sa62 4bb | sa624bb | Pembrokeshire | Sir Benfro | Spittal WwTW | 3274 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 195843 | 219593 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BJ | SA624BJ | sa62 4bj | sa624bj | Pembrokeshire | Sir Benfro | Spittal WwTW | 4534 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 196886 | 217990 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BL | SA624BL | sa62 4bl | sa624bl | Pembrokeshire | Sir Benfro | Camrose WwTW | 4464 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196011 | 217282 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BN | SA624BN | sa62 4bn | sa624bn | Pembrokeshire | Sir Benfro | Camrose WwTW | 4200 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 196086 | 217852 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BP | SA624BP | sa62 4bp | sa624bp | Pembrokeshire | Sir Benfro | Camrose WwTW | 4183 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195761 | 217419 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BQ | SA624BQ | sa62 4bq | sa624bq | Pembrokeshire | Sir Benfro | Camrose WwTW | 4369 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 195939 | 217345 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BR | SA624BR | sa62 4br | sa624br | Pembrokeshire | Sir Benfro | Camrose WwTW | 4108 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 196062 | 217992 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BS | SA624BS | sa62 4bs | sa624bs | Pembrokeshire | Sir Benfro | Camrose WwTW | 4182 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 196200 | 218090 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BT | SA624BT | sa62 4bt | sa624bt | Pembrokeshire | Sir Benfro | Camrose WwTW | 3821 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 195658 | 217888 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BU | SA624BU | sa62 4bu | sa624bu | Pembrokeshire | Sir Benfro | Camrose WwTW | 3280 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 195483 | 218675 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BW | SA624BW | sa62 4bw | sa624bw | Pembrokeshire | Sir Benfro | Camrose WwTW | 4057 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 196240 | 218467 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BX | SA624BX | sa62 4bx | sa624bx | Pembrokeshire | Sir Benfro | Camrose WwTW | 2105 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 194588 | 219770 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BY | SA624BY | sa62 4by | sa624by | Pembrokeshire | Sir Benfro | Camrose WwTW | 3100 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 195568 | 219590 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4BZ | SA624BZ | sa62 4bz | sa624bz | Pembrokeshire | Sir Benfro | Camrose WwTW | 3104 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 195573 | 219602 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DA | SA624DA | sa62 4da | sa624da | Pembrokeshire | Sir Benfro | Treffgarne STW | 2581 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 195353 | 220417 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DB | SA624DB | sa62 4db | sa624db | Pembrokeshire | Sir Benfro | Spittal WwTW | 2379 | 1209 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.53 | 12.02 | 13.28 | 196074 | 220491 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DD | SA624DD | sa62 4dd | sa624dd | Pembrokeshire | Sir Benfro | Spittal WwTW | 2751 | 1219 | 1200to1500 | 2.44 | 1.79 | 1.31 | 22.72 | 12.12 | 13.39 | 196752 | 219815 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DE | SA624DE | sa62 4de | sa624de | Pembrokeshire | Sir Benfro | Spittal WwTW | 3488 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 197216 | 219015 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DF | SA624DF | sa62 4df | sa624df | Pembrokeshire | Sir Benfro | Spittal WwTW | 4057 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 197194 | 218446 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DG | SA624DG | sa62 4dg | sa624dg | Pembrokeshire | Sir Benfro | Spittal WwTW | 4407 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 196983 | 218109 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DH | SA624DH | sa62 4dh | sa624dh | Pembrokeshire | Sir Benfro | Spittal WwTW | 4583 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 196839 | 217946 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DJ | SA624DJ | sa62 4dj | sa624dj | Pembrokeshire | Sir Benfro | Spittal WwTW | 4632 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 197128 | 217874 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DL | SA624DL | sa62 4dl | sa624dl | Pembrokeshire | Sir Benfro | Spittal WwTW | 4461 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 197115 | 218046 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DN | SA624DN | sa62 4dn | sa624dn | Pembrokeshire | Sir Benfro | Spittal WwTW | 4444 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 196790 | 218092 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DP | SA624DP | sa62 4dp | sa624dp | Pembrokeshire | Sir Benfro | Spittal WwTW | 4385 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 197245 | 218117 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DQ | SA624DQ | sa62 4dq | sa624dq | Pembrokeshire | Sir Benfro | Spittal WwTW | 4557 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 196696 | 217990 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DR | SA624DR | sa62 4dr | sa624dr | Pembrokeshire | Sir Benfro | Spittal WwTW | 4362 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 197094 | 218146 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DS | SA624DS | sa62 4ds | sa624ds | Pembrokeshire | Sir Benfro | Spittal WwTW | 3463 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 197441 | 219039 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DT | SA624DT | sa62 4dt | sa624dt | Pembrokeshire | Sir Benfro | Spittal WwTW | 2986 | 1234 | 1200to1500 | 2.47 | 1.81 | 1.33 | 23 | 12.27 | 13.56 | 197828 | 219554 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DU | SA624DU | sa62 4du | sa624du | Pembrokeshire | Sir Benfro | Spittal WwTW | 2950 | 1234 | 1200to1500 | 2.47 | 1.81 | 1.33 | 23 | 12.27 | 13.56 | 197922 | 219607 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DW | SA624DW | sa62 4dw | sa624dw | Pembrokeshire | Sir Benfro | Spittal WwTW | 4265 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 197166 | 218239 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DX | SA624DX | sa62 4dx | sa624dx | Pembrokeshire | Sir Benfro | Spittal WwTW | 2195 | 1234 | 1200to1500 | 2.47 | 1.81 | 1.33 | 23 | 12.27 | 13.56 | 197514 | 220312 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DY | SA624DY | sa62 4dy | sa624dy | Pembrokeshire | Sir Benfro | Spittal WwTW | 3381 | 1214 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.63 | 12.07 | 13.34 | 198189 | 219226 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4DZ | SA624DZ | sa62 4dz | sa624dz | Pembrokeshire | Sir Benfro | Spittal WwTW | 4306 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 197226 | 218196 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EB | SA624EB | sa62 4eb | sa624eb | Pembrokeshire | Sir Benfro | Spittal WwTW | 2447 | 1252 | 1200to1500 | 2.51 | 1.83 | 1.34 | 23.34 | 12.45 | 13.76 | 198602 | 220400 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4ED | SA624ED | sa62 4ed | sa624ed | Pembrokeshire | Sir Benfro | Spittal WwTW | 1867 | 1256 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.41 | 12.49 | 13.8 | 198194 | 220836 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EE | SA624EE | sa62 4ee | sa624ee | Pembrokeshire | Sir Benfro | Spittal WwTW | 2277 | 1265 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.58 | 12.57 | 13.9 | 198730 | 220691 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EF | SA624EF | sa62 4ef | sa624ef | Pembrokeshire | Sir Benfro | Spittal WwTW | 4605 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 196783 | 217930 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EG | SA624EG | sa62 4eg | sa624eg | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 3146 | 1214 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.63 | 12.07 | 13.34 | 198361 | 219411 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EH | SA624EH | sa62 4eh | sa624eh | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 2607 | 1252 | 1200to1500 | 2.51 | 1.83 | 1.34 | 23.34 | 12.45 | 13.76 | 198934 | 219510 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EJ | SA624EJ | sa62 4ej | sa624ej | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 1625 | 1303 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.29 | 12.95 | 14.32 | 199725 | 220094 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EL | SA624EL | sa62 4el | sa624el | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 1951 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 200140 | 219266 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EN | SA624EN | sa62 4en | sa624en | Pembrokeshire | Sir Benfro | Spittal WwTW | 4004 | 1214 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.63 | 12.07 | 13.34 | 197688 | 218511 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EP | SA624EP | sa62 4ep | sa624ep | Pembrokeshire | Sir Benfro | Spittal WwTW | 4502 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 196963 | 218015 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EQ | SA624EQ | sa62 4eq | sa624eq | Pembrokeshire | Sir Benfro | Camrose WwTW | 4065 | 1183 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.05 | 11.76 | 13 | 195924 | 217848 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4ER | SA624ER | sa62 4er | sa624er | Pembrokeshire | Sir Benfro | Spittal WwTW | 4468 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 197011 | 218045 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EW | SA624EW | sa62 4ew | sa624ew | Pembrokeshire | Sir Benfro | Spittal WwTW | 4645 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 196796 | 217888 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4EZ | SA624EZ | sa62 4ez | sa624ez | Pembrokeshire | Sir Benfro | Spittal WwTW | 4570 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 196990 | 217945 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4FD | SA624FD | sa62 4fd | sa624fd | Pembrokeshire | Sir Benfro | Camrose WwTW | 4771 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 196682 | 217742 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4FE | SA624FE | sa62 4fe | sa624fe | Pembrokeshire | Sir Benfro | Spittal WwTW | 4644 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 197011 | 217869 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4FG | SA624FG | sa62 4fg | sa624fg | Pembrokeshire | Sir Benfro | Spittal WwTW | 4296 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 196897 | 218228 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PH | SA624PH | sa62 4ph | sa624ph | Pembrokeshire | Sir Benfro | Wiston STW | 1902 | 1288 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.01 | 12.8 | 14.15 | 203777 | 216200 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PJ | SA624PJ | sa62 4pj | sa624pj | Pembrokeshire | Sir Benfro | Wiston STW | 833 | 1269 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.65 | 12.61 | 13.94 | 202131 | 217035 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PL | SA624PL | sa62 4pl | sa624pl | Pembrokeshire | Sir Benfro | Wiston STW | 558 | 1303 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.29 | 12.95 | 14.32 | 202114 | 217945 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PN | SA624PN | sa62 4pn | sa624pn | Pembrokeshire | Sir Benfro | Wiston STW | 498 | 1303 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.29 | 12.95 | 14.32 | 202338 | 218121 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PP | SA624PP | sa62 4pp | sa624pp | Pembrokeshire | Sir Benfro | Wiston STW | 947 | 1320 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.6 | 13.12 | 14.5 | 202447 | 218641 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PR | SA624PR | sa62 4pr | sa624pr | Pembrokeshire | Sir Benfro | Wiston STW | 237 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 202839 | 217801 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PS | SA624PS | sa62 4ps | sa624ps | Pembrokeshire | Sir Benfro | Wiston STW | 796 | 1303 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.29 | 12.95 | 14.32 | 201939 | 218122 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PT | SA624PT | sa62 4pt | sa624pt | Pembrokeshire | Sir Benfro | Wiston STW | 1493 | 1265 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.58 | 12.57 | 13.9 | 201258 | 218321 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PU | SA624PU | sa62 4pu | sa624pu | Pembrokeshire | Sir Benfro | Wiston STW | 2218 | 1278 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.82 | 12.7 | 14.04 | 200493 | 218339 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PW | SA624PW | sa62 4pw | sa624pw | Pembrokeshire | Sir Benfro | Wiston STW | 715 | 1303 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.29 | 12.95 | 14.32 | 202055 | 218149 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PX | SA624PX | sa62 4px | sa624px | Pembrokeshire | Sir Benfro | Wiston STW | 2803 | 1278 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.82 | 12.7 | 14.04 | 199888 | 218336 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PY | SA624PY | sa62 4py | sa624py | Pembrokeshire | Sir Benfro | Wiston STW | 3707 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 198921 | 217458 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4PZ | SA624PZ | sa62 4pz | sa624pz | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 4330 | 1208 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.52 | 12.01 | 13.27 | 198112 | 217829 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4QA | SA624QA | sa62 4qa | sa624qa | Pembrokeshire | Sir Benfro | Wiston STW | 555 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 202508 | 218254 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4QB | SA624QB | sa62 4qb | sa624qb | Pembrokeshire | Sir Benfro | Wiston STW | 1545 | 1354 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.24 | 13.46 | 14.88 | 203875 | 218611 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 4QD | SA624QD | sa62 4qd | sa624qd | Pembrokeshire | Sir Benfro | Llawhaden STW | 2181 | 1357 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.29 | 13.49 | 14.91 | 205393 | 219266 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5AB | SA625AB | sa62 5ab | sa625ab | Pembrokeshire | Sir Benfro | Mathry STW | 3443 | 1223 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.79 | 12.16 | 13.44 | 185632 | 229267 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5AQ | SA625AQ | sa62 5aq | sa625aq | Pembrokeshire | Sir Benfro | Letterston West STW | 3859 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 190609 | 226044 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5AW | SA625AW | sa62 5aw | sa625aw | Pembrokeshire | Sir Benfro | Letterston West STW | 2100 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 194903 | 229782 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DA | SA625DA | sa62 5da | sa625da | Pembrokeshire | Sir Benfro | Treffgarne STW | 543 | 1252 | 1200to1500 | 2.51 | 1.83 | 1.34 | 23.34 | 12.45 | 13.76 | 196315 | 222670 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DB | SA625DB | sa62 5db | sa625db | Pembrokeshire | Sir Benfro | Spittal WwTW | 881 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 196865 | 223238 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DD | SA625DD | sa62 5dd | sa625dd | Pembrokeshire | Sir Benfro | Treffgarne STW | 2255 | 1324 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.68 | 13.16 | 14.55 | 197182 | 224770 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DE | SA625DE | sa62 5de | sa625de | Pembrokeshire | Sir Benfro | Spittal WwTW | 1546 | 1301 | 1200to1500 | 2.6 | 1.91 | 1.4 | 24.25 | 12.93 | 14.29 | 197304 | 224047 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DG | SA625DG | sa62 5dg | sa625dg | Pembrokeshire | Sir Benfro | Spittal WwTW | 1861 | 1367 | 1200to1500 | 2.74 | 2 | 1.47 | 25.48 | 13.59 | 15.02 | 197808 | 224304 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DH | SA625DH | sa62 5dh | sa625dh | Pembrokeshire | Sir Benfro | Ambleston STW | 2432 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 198430 | 226707 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DJ | SA625DJ | sa62 5dj | sa625dj | Pembrokeshire | Sir Benfro | Puncheston WwTW | 2372 | 1429 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.63 | 14.2 | 15.7 | 199103 | 228380 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DL | SA625DL | sa62 5dl | sa625dl | Pembrokeshire | Sir Benfro | Puncheston WwTW | 548 | 1507 | Over1500 | 3.02 | 2.21 | 1.62 | 28.09 | 14.98 | 16.56 | 200912 | 229286 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 5DN | SA625DN | sa62 5dn | sa625dn | Pembrokeshire | Sir Benfro | Puncheston WwTW | 1493 | 1571 | Over1500 | 3.14 | 2.3 | 1.69 | 29.28 | 15.62 | 17.26 | 202142 | 228893 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DP | SA625DP | sa62 5dp | sa625dp | Pembrokeshire | Sir Benfro | Ambleston STW | 2243 | 1442 | 1200to1500 | 2.89 | 2.11 | 1.55 | 26.88 | 14.33 | 15.84 | 199978 | 227449 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DQ | SA625DQ | sa62 5dq | sa625dq | Pembrokeshire | Sir Benfro | Ambleston STW | 2159 | 1351 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.18 | 13.43 | 14.84 | 198211 | 225204 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DR | SA625DR | sa62 5dr | sa625dr | Pembrokeshire | Sir Benfro | Ambleston STW | 1514 | 1432 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.69 | 14.23 | 15.73 | 199459 | 226450 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DS | SA625DS | sa62 5ds | sa625ds | Pembrokeshire | Sir Benfro | Wolfscastle STW | 2185 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 197985 | 226611 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DT | SA625DT | sa62 5dt | sa625dt | Pembrokeshire | Sir Benfro | Wolfscastle STW | 1438 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 196865 | 227566 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DU | SA625DU | sa62 5du | sa625du | Pembrokeshire | Sir Benfro | Wolfscastle STW | 2333 | 1404 | 1200to1500 | 2.81 | 2.06 | 1.51 | 26.17 | 13.96 | 15.43 | 198103 | 226974 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DW | SA625DW | sa62 5dw | sa625dw | Pembrokeshire | Sir Benfro | Castlemorris Wastewater Treatment | 528 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 190203 | 231512 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DX | SA625DX | sa62 5dx | sa625dx | Pembrokeshire | Sir Benfro | Wolfscastle STW | 611 | 1363 | 1200to1500 | 2.73 | 2 | 1.46 | 25.4 | 13.55 | 14.98 | 196406 | 226525 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DY | SA625DY | sa62 5dy | sa625dy | Pembrokeshire | Sir Benfro | Wolfscastle STW | 1687 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 197315 | 225858 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5DZ | SA625DZ | sa62 5dz | sa625dz | Pembrokeshire | Sir Benfro | Wolfscastle STW | 1697 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 196308 | 224981 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EA | SA625EA | sa62 5ea | sa625ea | Pembrokeshire | Sir Benfro | Spittal WwTW | 1721 | 1301 | 1200to1500 | 2.6 | 1.91 | 1.4 | 24.25 | 12.93 | 14.29 | 197188 | 224215 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EE | SA625EE | sa62 5ee | sa625ee | Pembrokeshire | Sir Benfro | Letterston West STW | 1468 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 192893 | 230618 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EG | SA625EG | sa62 5eg | sa625eg | Pembrokeshire | Sir Benfro | Letterston West STW | 1478 | 1262 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.52 | 12.54 | 13.87 | 192399 | 230541 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EH | SA625EH | sa62 5eh | sa625eh | Pembrokeshire | Sir Benfro | Letterston West STW | 1781 | 1315 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.51 | 13.07 | 14.45 | 191555 | 230318 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EJ | SA625EJ | sa62 5ej | sa625ej | Pembrokeshire | Sir Benfro | Castlemorris Wastewater Treatment | 1776 | 1308 | 1200to1500 | 2.62 | 1.92 | 1.4 | 24.38 | 13 | 14.37 | 190854 | 230219 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EL | SA625EL | sa62 5el | sa625el | Pembrokeshire | Sir Benfro | Castlemorris Wastewater Treatment | 2381 | 1299 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.21 | 12.91 | 14.27 | 189979 | 229631 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EN | SA625EN | sa62 5en | sa625en | Pembrokeshire | Sir Benfro | Castlemorris Wastewater Treatment | 1286 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 189994 | 230770 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EP | SA625EP | sa62 5ep | sa625ep | Pembrokeshire | Sir Benfro | Castlemorris Wastewater Treatment | 591 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 190165 | 231462 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EQ | SA625EQ | sa62 5eq | sa625eq | Pembrokeshire | Sir Benfro | Castlemorris Wastewater Treatment | 615 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 190259 | 231386 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5ER | SA625ER | sa62 5er | sa625er | Pembrokeshire | Sir Benfro | Castlemorris Wastewater Treatment | 479 | 1202 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.4 | 11.95 | 13.21 | 190234 | 231551 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5ES | SA625ES | sa62 5es | sa625es | Pembrokeshire | Sir Benfro | Mathry STW | 938 | 1222 | 1200to1500 | 2.45 | 1.79 | 1.31 | 22.78 | 12.15 | 13.43 | 189223 | 231080 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5ET | SA625ET | sa62 5et | sa625et | Pembrokeshire | Sir Benfro | Castlemorris Wastewater Treatment | 448 | 1272 | 1200to1500 | 2.55 | 1.86 | 1.37 | 23.71 | 12.64 | 13.98 | 190544 | 232402 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EW | SA625EW | sa62 5ew | sa625ew | Pembrokeshire | Sir Benfro | Castlemorris Wastewater Treatment | 600 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 190224 | 231418 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EX | SA625EX | sa62 5ex | sa625ex | Pembrokeshire | Sir Benfro | Mathry STW | 438 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 188063 | 231735 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EY | SA625EY | sa62 5ey | sa625ey | Pembrokeshire | Sir Benfro | Mathry STW | 509 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 188002 | 231777 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5EZ | SA625EZ | sa62 5ez | sa625ez | Pembrokeshire | Sir Benfro | Mathry STW | 683 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 187860 | 231882 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5FA | SA625FA | sa62 5fa | sa625fa | Pembrokeshire | Sir Benfro | Mathry STW | 627 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 187914 | 231856 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5HB | SA625HB | sa62 5hb | sa625hb | Pembrokeshire | Sir Benfro | Mathry STW | 611 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 188026 | 231920 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5HQ | SA625HQ | sa62 5hq | sa625hq | Pembrokeshire | Sir Benfro | Mathry STW | 671 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 187909 | 231910 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5HS | SA625HS | sa62 5hs | sa625hs | Pembrokeshire | Sir Benfro | Letterston West STW | 3578 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 189858 | 227266 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5HT | SA625HT | sa62 5ht | sa625ht | Pembrokeshire | Sir Benfro | Mathry STW | 3547 | 1257 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.43 | 12.5 | 13.81 | 189346 | 227993 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5JB | SA625JB | sa62 5jb | sa625jb | Pembrokeshire | Sir Benfro | Mathry STW | 498 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 187889 | 231181 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5JD | SA625JD | sa62 5jd | sa625jd | Pembrokeshire | Sir Benfro | Mathry STW | 1194 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 187251 | 230903 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5JE | SA625JE | sa62 5je | sa625je | Pembrokeshire | Sir Benfro | Mathry STW | 3046 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 185812 | 229693 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5JG | SA625JG | sa62 5jg | sa625jg | Pembrokeshire | Sir Benfro | Mathry STW | 683 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 187713 | 231668 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5JN | SA625JN | sa62 5jn | sa625jn | Pembrokeshire | Sir Benfro | Mathry STW | 4293 | 1104 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.58 | 10.97 | 12.13 | 184089 | 230782 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5JW | SA625JW | sa62 5jw | sa625jw | Pembrokeshire | Sir Benfro | Mathry STW | 4229 | 1104 | 900to1200 | 2.21 | 1.62 | 1.19 | 20.58 | 10.97 | 12.13 | 184147 | 230831 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5JX | SA625JX | sa62 5jx | sa625jx | Pembrokeshire | Sir Benfro | Mathry STW | 4043 | 1145 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.34 | 11.38 | 12.58 | 184412 | 230432 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5LL | SA625LL | sa62 5ll | sa625ll | Pembrokeshire | Sir Benfro | Mathry STW | 774 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 188351 | 230621 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5LN | SA625LN | sa62 5ln | sa625ln | Pembrokeshire | Sir Benfro | Treffgarne STW | 654 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 195708 | 222312 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5LP | SA625LP | sa62 5lp | sa625lp | Pembrokeshire | Sir Benfro | Treffgarne STW | 430 | 1252 | 1200to1500 | 2.51 | 1.83 | 1.34 | 23.34 | 12.45 | 13.76 | 196043 | 223334 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5LR | SA625LR | sa62 5lr | sa625lr | Pembrokeshire | Sir Benfro | Wolfscastle STW | 1340 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 195630 | 225271 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5LS | SA625LS | sa62 5ls | sa625ls | Pembrokeshire | Sir Benfro | Wolfscastle STW | 506 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 195725 | 226100 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5LT | SA625LT | sa62 5lt | sa625lt | Pembrokeshire | Sir Benfro | Wolfscastle STW | 356 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 195586 | 226315 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5LU | SA625LU | sa62 5lu | sa625lu | Pembrokeshire | Sir Benfro | Wolfscastle STW | 283 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 195684 | 226342 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5LW | SA625LW | sa62 5lw | sa625lw | Pembrokeshire | Sir Benfro | Treffgarne STW | 410 | 1252 | 1200to1500 | 2.51 | 1.83 | 1.34 | 23.34 | 12.45 | 13.76 | 195521 | 222706 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5LX | SA625LX | sa62 5lx | sa625lx | Pembrokeshire | Sir Benfro | Wolfscastle STW | 494 | 1375 | 1200to1500 | 2.75 | 2.01 | 1.48 | 25.63 | 13.67 | 15.11 | 196056 | 226177 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5LY | SA625LY | sa62 5ly | sa625ly | Pembrokeshire | Sir Benfro | Wolfscastle STW | 163 | 1363 | 1200to1500 | 2.73 | 2 | 1.46 | 25.4 | 13.55 | 14.98 | 195649 | 226539 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5LZ | SA625LZ | sa62 5lz | sa625lz | Pembrokeshire | Sir Benfro | Wolfscastle STW | 246 | 1363 | 1200to1500 | 2.73 | 2 | 1.46 | 25.4 | 13.55 | 14.98 | 195563 | 226665 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NA | SA625NA | sa62 5na | sa625na | Pembrokeshire | Sir Benfro | Wolfscastle STW | 607 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 195222 | 226786 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NB | SA625NB | sa62 5nb | sa625nb | Pembrokeshire | Sir Benfro | Wolfscastle STW | 184 | 1363 | 1200to1500 | 2.73 | 2 | 1.46 | 25.4 | 13.55 | 14.98 | 195748 | 226777 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5ND | SA625ND | sa62 5nd | sa625nd | Pembrokeshire | Sir Benfro | Wolfscastle STW | 495 | 1363 | 1200to1500 | 2.73 | 2 | 1.46 | 25.4 | 13.55 | 14.98 | 195768 | 227094 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NE | SA625NE | sa62 5ne | sa625ne | Pembrokeshire | Sir Benfro | Wolfscastle STW | 1444 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 196118 | 228009 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NF | SA625NF | sa62 5nf | sa625nf | Pembrokeshire | Sir Benfro | Wolfscastle STW | 1664 | 1381 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.74 | 13.73 | 15.17 | 196628 | 228044 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NG | SA625NG | sa62 5ng | sa625ng | Pembrokeshire | Sir Benfro | Wolfscastle STW | 1917 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 196072 | 228498 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NH | SA625NH | sa62 5nh | sa625nh | Pembrokeshire | Sir Benfro | Wolfscastle STW | 1681 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 194995 | 228076 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NJ | SA625NJ | sa62 5nj | sa625nj | Pembrokeshire | Sir Benfro | Wolfscastle STW | 1450 | 1310 | 1200to1500 | 2.62 | 1.92 | 1.41 | 24.42 | 13.02 | 14.39 | 194997 | 227808 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NL | SA625NL | sa62 5nl | sa625nl | Pembrokeshire | Sir Benfro | Letterston West STW | 1835 | 1267 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.61 | 12.59 | 13.92 | 194368 | 228049 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NN | SA625NN | sa62 5nn | sa625nn | Pembrokeshire | Sir Benfro | Letterston West STW | 1462 | 1267 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.61 | 12.59 | 13.92 | 193517 | 227824 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NP | SA625NP | sa62 5np | sa625np | Pembrokeshire | Sir Benfro | Letterston West STW | 883 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 192067 | 228856 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NR | SA625NR | sa62 5nr | sa625nr | Pembrokeshire | Sir Benfro | Letterston West STW | 1658 | 1262 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.52 | 12.54 | 13.87 | 193256 | 227530 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NS | SA625NS | sa62 5ns | sa625ns | Pembrokeshire | Sir Benfro | Letterston West STW | 2572 | 1285 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.95 | 12.77 | 14.12 | 193172 | 226592 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NT | SA625NT | sa62 5nt | sa625nt | Pembrokeshire | Sir Benfro | Letterston West STW | 2314 | 1285 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.95 | 12.77 | 14.12 | 192577 | 226858 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NU | SA625NU | sa62 5nu | sa625nu | Pembrokeshire | Sir Benfro | Letterston West STW | 2225 | 1273 | 1200to1500 | 2.55 | 1.86 | 1.37 | 23.73 | 12.65 | 13.99 | 192126 | 227064 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NX | SA625NX | sa62 5nx | sa625nx | Pembrokeshire | Sir Benfro | Letterston West STW | 2802 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 192659 | 226358 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5NY | SA625NY | sa62 5ny | sa625ny | Pembrokeshire | Sir Benfro | Letterston West STW | 4053 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 191449 | 225365 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5PA | SA625PA | sa62 5pa | sa625pa | Pembrokeshire | Sir Benfro | Wolfscastle STW | 1575 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 194371 | 225938 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5PE | SA625PE | sa62 5pe | sa625pe | Pembrokeshire | Sir Benfro | Treffgarne STW | 1860 | 1229 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.91 | 12.22 | 13.5 | 195863 | 221090 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5PG | SA625PG | sa62 5pg | sa625pg | Pembrokeshire | Sir Benfro | Treffgarne STW | 1124 | 1217 | 1200to1500 | 2.44 | 1.78 | 1.31 | 22.68 | 12.1 | 13.37 | 195752 | 221830 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5PH | SA625PH | sa62 5ph | sa625ph | Pembrokeshire | Sir Benfro | Treffgarne STW | 717 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 195664 | 223643 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5PJ | SA625PJ | sa62 5pj | sa625pj | Pembrokeshire | Sir Benfro | Treffgarne STW | 994 | 1260 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.48 | 12.53 | 13.84 | 195178 | 223682 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5PL | SA625PL | sa62 5pl | sa625pl | Pembrokeshire | Sir Benfro | Treffgarne STW | 1670 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 194339 | 223661 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5PN | SA625PN | sa62 5pn | sa625pn | Pembrokeshire | Sir Benfro | Treffgarne STW | 3970 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 192019 | 223994 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5PQ | SA625PQ | sa62 5pq | sa625pq | Pembrokeshire | Sir Benfro | Treffgarne STW | 665 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 195624 | 223575 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5PR | SA625PR | sa62 5pr | sa625pr | Pembrokeshire | Sir Benfro | Letterston West STW | 4307 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 191384 | 225118 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5PW | SA625PW | sa62 5pw | sa625pw | Pembrokeshire | Sir Benfro | Wolfscastle STW | 3113 | 1291 | 1200to1500 | 2.58 | 1.89 | 1.39 | 24.06 | 12.83 | 14.18 | 193084 | 225078 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5PZ | SA625PZ | sa62 5pz | sa625pz | Pembrokeshire | Sir Benfro | Letterston West STW | 1227 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 194060 | 229550 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QA | SA625QA | sa62 5qa | sa625qa | Pembrokeshire | Sir Benfro | Letterston West STW | 3713 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 190520 | 226300 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QB | SA625QB | sa62 5qb | sa625qb | Pembrokeshire | Sir Benfro | Letterston West STW | 3791 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 190518 | 226200 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QD | SA625QD | sa62 5qd | sa625qd | Pembrokeshire | Sir Benfro | Letterston West STW | 3377 | 1279 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.84 | 12.71 | 14.05 | 190664 | 226619 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QE | SA625QE | sa62 5qe | sa625qe | Pembrokeshire | Sir Benfro | Letterston West STW | 2702 | 1276 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.78 | 12.68 | 14.02 | 190392 | 228145 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QF | SA625QF | sa62 5qf | sa625qf | Pembrokeshire | Sir Benfro | Letterston West STW | 1525 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 191391 | 228931 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QG | SA625QG | sa62 5qg | sa625qg | Pembrokeshire | Sir Benfro | Letterston West STW | 3941 | 1332 | 1200to1500 | 2.67 | 1.95 | 1.43 | 24.83 | 13.24 | 14.63 | 190886 | 225762 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QH | SA625QH | sa62 5qh | sa625qh | Pembrokeshire | Sir Benfro | Spittal WwTW | 350 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 197438 | 222839 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QJ | SA625QJ | sa62 5qj | sa625qj | Pembrokeshire | Sir Benfro | Camrose WwTW | 4749 | 1160 | 900to1200 | 2.32 | 1.7 | 1.25 | 21.62 | 11.53 | 12.74 | 196485 | 217456 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QL | SA625QL | sa62 5ql | sa625ql | Pembrokeshire | Sir Benfro | Spittal WwTW | 1829 | 1294 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.12 | 12.86 | 14.22 | 199005 | 221726 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QN | SA625QN | sa62 5qn | sa625qn | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 1269 | 1312 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.45 | 13.04 | 14.41 | 200440 | 222054 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QP | SA625QP | sa62 5qp | sa625qp | Pembrokeshire | Sir Benfro | Spittal WwTW | 508 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 197573 | 222956 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QQ | SA625QQ | sa62 5qq | sa625qq | Pembrokeshire | Sir Benfro | Spittal WwTW | 455 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 197396 | 222954 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QR | SA625QR | sa62 5qr | sa625qr | Pembrokeshire | Sir Benfro | Spittal WwTW | 655 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 197175 | 223133 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QS | SA625QS | sa62 5qs | sa625qs | Pembrokeshire | Sir Benfro | Spittal WwTW | 654 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 197559 | 223120 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QT | SA625QT | sa62 5qt | sa625qt | Pembrokeshire | Sir Benfro | Spittal WwTW | 777 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 197725 | 223181 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QU | SA625QU | sa62 5qu | sa625qu | Pembrokeshire | Sir Benfro | Spittal WwTW | 1510 | 1367 | 1200to1500 | 2.74 | 2 | 1.47 | 25.48 | 13.59 | 15.02 | 197795 | 223943 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QW | SA625QW | sa62 5qw | sa625qw | Pembrokeshire | Sir Benfro | Spittal WwTW | 662 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 197757 | 223022 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QX | SA625QX | sa62 5qx | sa625qx | Pembrokeshire | Sir Benfro | Ambleston STW | 1471 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 198942 | 224887 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QY | SA625QY | sa62 5qy | sa625qy | Pembrokeshire | Sir Benfro | Ambleston STW | 595 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 200092 | 225766 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5QZ | SA625QZ | sa62 5qz | sa625qz | Pembrokeshire | Sir Benfro | Ambleston STW | 535 | 1479 | 1200to1500 | 2.96 | 2.17 | 1.59 | 27.57 | 14.7 | 16.25 | 200218 | 225753 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RA | SA625RA | sa62 5ra | sa625ra | Pembrokeshire | Sir Benfro | Ambleston STW | 720 | 1526 | Over1500 | 3.05 | 2.23 | 1.64 | 28.44 | 15.17 | 16.77 | 200900 | 225727 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RB | SA625RB | sa62 5rb | sa625rb | Pembrokeshire | Sir Benfro | Ambleston STW | 1112 | 1526 | Over1500 | 3.05 | 2.23 | 1.64 | 28.44 | 15.17 | 16.77 | 201318 | 225821 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RD | SA625RD | sa62 5rd | sa625rd | Pembrokeshire | Sir Benfro | Ambleston STW | 966 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 200369 | 224274 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RE | SA625RE | sa62 5re | sa625re | Pembrokeshire | Sir Benfro | Ambleston STW | 1620 | 1412 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.32 | 14.04 | 15.51 | 199568 | 223832 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RF | SA625RF | sa62 5rf | sa625rf | Pembrokeshire | Sir Benfro | Ambleston STW | 1984 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 199544 | 223436 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RG | SA625RG | sa62 5rg | sa625rg | Pembrokeshire | Sir Benfro | Treffgarne STW | 641 | 1252 | 1200to1500 | 2.51 | 1.83 | 1.34 | 23.34 | 12.45 | 13.76 | 196382 | 223308 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RH | SA625RH | sa62 5rh | sa625rh | Pembrokeshire | Sir Benfro | Puncheston WwTW | 486 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 200517 | 229682 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RJ | SA625RJ | sa62 5rj | sa625rj | Pembrokeshire | Sir Benfro | Puncheston WwTW | 310 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 200698 | 229701 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RL | SA625RL | sa62 5rl | sa625rl | Pembrokeshire | Sir Benfro | Puncheston WwTW | 357 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 200627 | 229776 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RN | SA625RN | sa62 5rn | sa625rn | Pembrokeshire | Sir Benfro | Puncheston WwTW | 122 | 1530 | Over1500 | 3.06 | 2.24 | 1.64 | 28.52 | 15.21 | 16.81 | 200889 | 229749 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RP | SA625RP | sa62 5rp | sa625rp | Pembrokeshire | Sir Benfro | Puncheston WwTW | 1036 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 201360 | 230794 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RQ | SA625RQ | sa62 5rq | sa625rq | Pembrokeshire | Sir Benfro | Letterston West STW | 2163 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 194959 | 229812 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RR | SA625RR | sa62 5rr | sa625rr | Pembrokeshire | Sir Benfro | Puncheston WwTW | 1249 | 1628 | Over1500 | 3.26 | 2.38 | 1.75 | 30.34 | 16.18 | 17.89 | 201530 | 230951 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RS | SA625RS | sa62 5rs | sa625rs | Pembrokeshire | Sir Benfro | Puncheston WwTW | 1410 | 1628 | Over1500 | 3.26 | 2.38 | 1.75 | 30.34 | 16.18 | 17.89 | 202026 | 230776 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RT | SA625RT | sa62 5rt | sa625rt | Pembrokeshire | Sir Benfro | Puncheston WwTW | 616 | 1616 | Over1500 | 3.23 | 2.37 | 1.74 | 30.12 | 16.06 | 17.75 | 201530 | 230107 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 5RU | SA625RU | sa62 5ru | sa625ru | Pembrokeshire | Sir Benfro | Puncheston WwTW | 624 | 1616 | Over1500 | 3.23 | 2.37 | 1.74 | 30.12 | 16.06 | 17.75 | 201583 | 229668 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 5RW | SA625RW | sa62 5rw | sa625rw | Pembrokeshire | Sir Benfro | Puncheston WwTW | 1019 | 1527 | Over1500 | 3.06 | 2.24 | 1.64 | 28.46 | 15.18 | 16.78 | 200711 | 230813 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RX | SA625RX | sa62 5rx | sa625rx | Pembrokeshire | Sir Benfro | Spittal WwTW | 731 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 197714 | 223134 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RY | SA625RY | sa62 5ry | sa625ry | Pembrokeshire | Sir Benfro | Letterston West STW | 2109 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 194901 | 229818 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5RZ | SA625RZ | sa62 5rz | sa625rz | Pembrokeshire | Sir Benfro | Letterston West STW | 2069 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 194851 | 229839 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SB | SA625SB | sa62 5sb | sa625sb | Pembrokeshire | Sir Benfro | Letterston West STW | 1684 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 194495 | 229692 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SD | SA625SD | sa62 5sd | sa625sd | Pembrokeshire | Sir Benfro | Letterston West STW | 1667 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 194456 | 229749 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SE | SA625SE | sa62 5se | sa625se | Pembrokeshire | Sir Benfro | Letterston West STW | 1539 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 194336 | 229705 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SF | SA625SF | sa62 5sf | sa625sf | Pembrokeshire | Sir Benfro | Letterston West STW | 1497 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 194312 | 229648 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SH | SA625SH | sa62 5sh | sa625sh | Pembrokeshire | Sir Benfro | Letterston West STW | 1413 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 194158 | 229794 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SJ | SA625SJ | sa62 5sj | sa625sj | Pembrokeshire | Sir Benfro | Letterston West STW | 1176 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 193970 | 229638 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SL | SA625SL | sa62 5sl | sa625sl | Pembrokeshire | Sir Benfro | Letterston West STW | 1123 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 193940 | 229575 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SN | SA625SN | sa62 5sn | sa625sn | Pembrokeshire | Sir Benfro | Letterston West STW | 950 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 193737 | 229599 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SP | SA625SP | sa62 5sp | sa625sp | Pembrokeshire | Sir Benfro | Letterston West STW | 1026 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 193720 | 229767 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SQ | SA625SQ | sa62 5sq | sa625sq | Pembrokeshire | Sir Benfro | Letterston West STW | 1407 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 194259 | 229514 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SR | SA625SR | sa62 5sr | sa625sr | Pembrokeshire | Sir Benfro | Letterston West STW | 793 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 193535 | 229625 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SS | SA625SS | sa62 5ss | sa625ss | Pembrokeshire | Sir Benfro | Letterston West STW | 902 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 193394 | 229905 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5ST | SA625ST | sa62 5st | sa625st | Pembrokeshire | Sir Benfro | Letterston West STW | 965 | 1293 | 1200to1500 | 2.59 | 1.89 | 1.39 | 24.1 | 12.85 | 14.21 | 193453 | 229941 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SU | SA625SU | sa62 5su | sa625su | Pembrokeshire | Sir Benfro | Letterston West STW | 942 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 193666 | 229699 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SW | SA625SW | sa62 5sw | sa625sw | Pembrokeshire | Sir Benfro | Letterston West STW | 1872 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 194644 | 229832 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SX | SA625SX | sa62 5sx | sa625sx | Pembrokeshire | Sir Benfro | Letterston West STW | 878 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 193547 | 229743 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SY | SA625SY | sa62 5sy | sa625sy | Pembrokeshire | Sir Benfro | Letterston West STW | 2622 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 195458 | 229728 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5SZ | SA625SZ | sa62 5sz | sa625sz | Pembrokeshire | Sir Benfro | Letterston West STW | 1267 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 194043 | 229697 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TA | SA625TA | sa62 5ta | sa625ta | Pembrokeshire | Sir Benfro | Letterston West STW | 2613 | 1353 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.22 | 13.45 | 14.87 | 195458 | 229683 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TB | SA625TB | sa62 5tb | sa625tb | Pembrokeshire | Sir Benfro | Wolfscastle STW | 3078 | 1361 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.37 | 13.53 | 14.95 | 196654 | 229557 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TD | SA625TD | sa62 5td | sa625td | Pembrokeshire | Sir Benfro | Puncheston WwTW | 3132 | 1385 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.81 | 13.77 | 15.22 | 197961 | 228995 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TE | SA625TE | sa62 5te | sa625te | Pembrokeshire | Sir Benfro | Puncheston WwTW | 3028 | 1429 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.63 | 14.2 | 15.7 | 198510 | 228078 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TF | SA625TF | sa62 5tf | sa625tf | Pembrokeshire | Sir Benfro | Letterston West STW | 1069 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 193893 | 229547 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TG | SA625TG | sa62 5tg | sa625tg | Pembrokeshire | Sir Benfro | Puncheston WwTW | 2451 | 1501 | Over1500 | 3 | 2.2 | 1.61 | 27.98 | 14.92 | 16.49 | 198537 | 229624 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TH | SA625TH | sa62 5th | sa625th | Pembrokeshire | Sir Benfro | Puncheston WwTW | 3399 | 1411 | 1200to1500 | 2.82 | 2.07 | 1.52 | 26.3 | 14.03 | 15.5 | 197583 | 229960 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TJ | SA625TJ | sa62 5tj | sa625tj | Pembrokeshire | Sir Benfro | Letterston West STW | 3549 | 1426 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.58 | 14.18 | 15.67 | 196018 | 230846 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TL | SA625TL | sa62 5tl | sa625tl | Pembrokeshire | Sir Benfro | Letterston West STW | 3997 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 195959 | 231724 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TN | SA625TN | sa62 5tn | sa625tn | Pembrokeshire | Sir Benfro | Puncheston WwTW | 4530 | 1393 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.96 | 13.85 | 15.3 | 196963 | 231925 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TP | SA625TP | sa62 5tp | sa625tp | Pembrokeshire | Sir Benfro | Puncheston WwTW | 3050 | 1456 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.14 | 14.47 | 16 | 198615 | 231757 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TR | SA625TR | sa62 5tr | sa625tr | Pembrokeshire | Sir Benfro | Puncheston WwTW | 1592 | 1501 | Over1500 | 3 | 2.2 | 1.61 | 27.98 | 14.92 | 16.49 | 199497 | 230408 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TS | SA625TS | sa62 5ts | sa625ts | Pembrokeshire | Sir Benfro | Puncheston WwTW | 1535 | 1501 | Over1500 | 3 | 2.2 | 1.61 | 27.98 | 14.92 | 16.49 | 199448 | 229730 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TT | SA625TT | sa62 5tt | sa625tt | Pembrokeshire | Sir Benfro | Letterston West STW | 2064 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 194447 | 230516 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5TU | SA625TU | sa62 5tu | sa625tu | Pembrokeshire | Sir Benfro | Letterston West STW | 441 | 1285 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.95 | 12.77 | 14.12 | 193203 | 228829 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5UA | SA625UA | sa62 5ua | sa625ua | Pembrokeshire | Sir Benfro | Letterston West STW | 1742 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 194631 | 229343 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5UB | SA625UB | sa62 5ub | sa625ub | Pembrokeshire | Sir Benfro | Letterston West STW | 1753 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 194653 | 229155 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5UD | SA625UD | sa62 5ud | sa625ud | Pembrokeshire | Sir Benfro | Wolfscastle STW | 2455 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 195438 | 229028 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5UE | SA625UE | sa62 5ue | sa625ue | Pembrokeshire | Sir Benfro | Letterston West STW | 1659 | 1287 | 1200to1500 | 2.58 | 1.88 | 1.38 | 23.99 | 12.79 | 14.14 | 194458 | 228580 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5UF | SA625UF | sa62 5uf | sa625uf | Pembrokeshire | Sir Benfro | Letterston West STW | 2136 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 195031 | 228998 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5UG | SA625UG | sa62 5ug | sa625ug | Pembrokeshire | Sir Benfro | Letterston West STW | 1596 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 194202 | 230073 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5UH | SA625UH | sa62 5uh | sa625uh | Pembrokeshire | Sir Benfro | Letterston West STW | 1920 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 194083 | 230663 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5UJ | SA625UJ | sa62 5uj | sa625uj | Pembrokeshire | Sir Benfro | Letterston West STW | 1788 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 193513 | 230830 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5UL | SA625UL | sa62 5ul | sa625ul | Pembrokeshire | Sir Benfro | Letterston West STW | 2230 | 1298 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.19 | 12.9 | 14.26 | 192840 | 231379 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5UN | SA625UN | sa62 5un | sa625un | Pembrokeshire | Sir Benfro | Panteg STW | 2091 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 192667 | 232713 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5UP | SA625UP | sa62 5up | sa625up | Pembrokeshire | Sir Benfro | Castlemorris Wastewater Treatment | 1264 | 1212 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.59 | 12.05 | 13.32 | 191199 | 233002 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5XA | SA625XA | sa62 5xa | sa625xa | Pembrokeshire | Sir Benfro | Panteg STW | 1648 | 1205 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.46 | 11.98 | 13.24 | 191434 | 233878 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5XB | SA625XB | sa62 5xb | sa625xb | Pembrokeshire | Sir Benfro | Letterston West STW | 3024 | 1267 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.61 | 12.59 | 13.92 | 194293 | 231834 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5XD | SA625XD | sa62 5xd | sa625xd | Pembrokeshire | Sir Benfro | Panteg STW | 3261 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 195402 | 232834 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5XE | SA625XE | sa62 5xe | sa625xe | Pembrokeshire | Sir Benfro | Panteg STW | 4374 | 1377 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.67 | 13.69 | 15.13 | 197011 | 233614 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5XG | SA625XG | sa62 5xg | sa625xg | Pembrokeshire | Sir Benfro | Panteg STW | 3834 | 1297 | 1200to1500 | 2.6 | 1.9 | 1.39 | 24.17 | 12.89 | 14.25 | 195495 | 232072 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5XJ | SA625XJ | sa62 5xj | sa625xj | Pembrokeshire | Sir Benfro | Letterston West STW | 2428 | 1329 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.77 | 13.21 | 14.6 | 194289 | 231142 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5XP | SA625XP | sa62 5xp | sa625xp | Pembrokeshire | Sir Benfro | Panteg STW | 4384 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 196667 | 232734 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5XR | SA625XR | sa62 5xr | sa625xr | Pembrokeshire | Sir Benfro | Panteg STW | 4018 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 196417 | 233050 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5XT | SA625XT | sa62 5xt | sa625xt | Pembrokeshire | Sir Benfro | Panteg STW | 4490 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 196772 | 232705 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5XU | SA625XU | sa62 5xu | sa625xu | Pembrokeshire | Sir Benfro | Puncheston WwTW | 4531 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 197419 | 232633 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5XX | SA625XX | sa62 5xx | sa625xx | Pembrokeshire | Sir Benfro | Puncheston WwTW | 4237 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 197683 | 232492 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5XY | SA625XY | sa62 5xy | sa625xy | Pembrokeshire | Sir Benfro | Puncheston WwTW | 4091 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 197865 | 232483 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5YA | SA625YA | sa62 5ya | sa625ya | Pembrokeshire | Sir Benfro | Puncheston WwTW | 3985 | 1415 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.37 | 14.07 | 15.55 | 198008 | 232486 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5YD | SA625YD | sa62 5yd | sa625yd | Pembrokeshire | Sir Benfro | Panteg STW | 4756 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 197021 | 232607 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5YH | SA625YH | sa62 5yh | sa625yh | Pembrokeshire | Sir Benfro | Treffgarne STW | 3120 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 192894 | 223948 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5YJ | SA625YJ | sa62 5yj | sa625yj | Pembrokeshire | Sir Benfro | Treffgarne STW | 2396 | 1268 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.63 | 12.6 | 13.93 | 193485 | 223335 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 5YL | SA625YL | sa62 5yl | sa625yl | Pembrokeshire | Sir Benfro | Treffgarne STW | 2678 | 1261 | 1200to1500 | 2.52 | 1.85 | 1.35 | 23.5 | 12.53 | 13.85 | 193654 | 224484 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6AA | SA626AA | sa62 6aa | sa626aa | Pembrokeshire | Sir Benfro | Keeston WwTW | 1356 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 191992 | 218005 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6AB | SA626AB | sa62 6ab | sa626ab | Pembrokeshire | Sir Benfro | Keeston WwTW | 1192 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 191836 | 218063 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6AD | SA626AD | sa62 6ad | sa626ad | Pembrokeshire | Sir Benfro | Keeston WwTW | 640 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 190196 | 218841 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6AE | SA626AE | sa62 6ae | sa626ae | Pembrokeshire | Sir Benfro | Keeston WwTW | 2737 | 1144 | 900to1200 | 2.29 | 1.68 | 1.23 | 21.32 | 11.37 | 12.57 | 188320 | 219803 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6AG | SA626AG | sa62 6ag | sa626ag | Pembrokeshire | Sir Benfro | Keeston WwTW | 3889 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 187828 | 221169 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6AQ | SA626AQ | sa62 6aq | sa626aq | Pembrokeshire | Sir Benfro | Keeston WwTW | 3767 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 188029 | 221215 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA62 6BG | SA626BG | sa62 6bg | sa626bg | Pembrokeshire | Sir Benfro | Keeston WwTW | 3898 | 1150 | 900to1200 | 2.3 | 1.68 | 1.24 | 21.43 | 11.43 | 12.63 | 187741 | 221075 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6BJ | SA626BJ | sa62 6bj | sa626bj | Pembrokeshire | Sir Benfro | Keeston WwTW | 1269 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 191905 | 218028 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6DQ | SA626DQ | sa62 6dq | sa626dq | Pembrokeshire | Sir Benfro | Camrose WwTW | 632 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 192727 | 220630 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6DY | SA626DY | sa62 6dy | sa626dy | Pembrokeshire | Sir Benfro | Keeston WwTW | 2067 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 188917 | 219497 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6DZ | SA626DZ | sa62 6dz | sa626dz | Pembrokeshire | Sir Benfro | Keeston WwTW | 1620 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 189292 | 219231 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EA | SA626EA | sa62 6ea | sa626ea | Pembrokeshire | Sir Benfro | Keeston WwTW | 2862 | 1165 | 900to1200 | 2.33 | 1.71 | 1.25 | 21.71 | 11.58 | 12.8 | 193302 | 217261 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EB | SA626EB | sa62 6eb | sa626eb | Pembrokeshire | Sir Benfro | Keeston WwTW | 1010 | 1184 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.07 | 11.77 | 13.01 | 191105 | 217710 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6ED | SA626ED | sa62 6ed | sa626ed | Pembrokeshire | Sir Benfro | Keeston WwTW | 237 | 1190 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.18 | 11.83 | 13.07 | 191032 | 218582 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EE | SA626EE | sa62 6ee | sa626ee | Pembrokeshire | Sir Benfro | Keeston WwTW | 984 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 190192 | 219440 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EF | SA626EF | sa62 6ef | sa626ef | Pembrokeshire | Sir Benfro | Keeston WwTW | 2005 | 1195 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.27 | 11.88 | 13.13 | 189043 | 219617 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EG | SA626EG | sa62 6eg | sa626eg | Pembrokeshire | Sir Benfro | Keeston WwTW | 1924 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 189057 | 219460 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EH | SA626EH | sa62 6eh | sa626eh | Pembrokeshire | Sir Benfro | Keeston WwTW | 1070 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 190032 | 219408 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EJ | SA626EJ | sa62 6ej | sa626ej | Pembrokeshire | Sir Benfro | Keeston WwTW | 1293 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 189583 | 219072 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EL | SA626EL | sa62 6el | sa626el | Pembrokeshire | Sir Benfro | Keeston WwTW | 1464 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 189576 | 219458 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EN | SA626EN | sa62 6en | sa626en | Pembrokeshire | Sir Benfro | Keeston WwTW | 1845 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 189161 | 219497 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EP | SA626EP | sa62 6ep | sa626ep | Pembrokeshire | Sir Benfro | Keeston WwTW | 1813 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 189119 | 219320 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EQ | SA626EQ | sa62 6eq | sa626eq | Pembrokeshire | Sir Benfro | Keeston WwTW | 2083 | 1195 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.27 | 11.88 | 13.13 | 189006 | 219711 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6ER | SA626ER | sa62 6er | sa626er | Pembrokeshire | Sir Benfro | Keeston WwTW | 1956 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 189003 | 219416 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6ES | SA626ES | sa62 6es | sa626es | Pembrokeshire | Sir Benfro | Keeston WwTW | 1971 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 188925 | 219238 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EU | SA626EU | sa62 6eu | sa626eu | Pembrokeshire | Sir Benfro | Keeston WwTW | 2016 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 188969 | 219490 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EW | SA626EW | sa62 6ew | sa626ew | Pembrokeshire | Sir Benfro | Keeston WwTW | 997 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 190017 | 219276 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EX | SA626EX | sa62 6ex | sa626ex | Pembrokeshire | Sir Benfro | Keeston WwTW | 2674 | 1139 | 900to1200 | 2.28 | 1.67 | 1.22 | 21.23 | 11.32 | 12.51 | 188177 | 218239 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EY | SA626EY | sa62 6ey | sa626ey | Pembrokeshire | Sir Benfro | Keeston WwTW | 2050 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 188928 | 219480 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6EZ | SA626EZ | sa62 6ez | sa626ez | Pembrokeshire | Sir Benfro | Keeston WwTW | 1777 | 1185 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.09 | 11.78 | 13.02 | 189137 | 219263 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6FB | SA626FB | sa62 6fb | sa626fb | Pembrokeshire | Sir Benfro | Keeston WwTW | 853 | 1188 | 900to1200 | 2.38 | 1.74 | 1.28 | 22.14 | 11.81 | 13.05 | 190154 | 219217 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6FE | SA626FE | sa62 6fe | sa626fe | Pembrokeshire | Sir Benfro | Camrose WwTW | 1642 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 193200 | 221526 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HA | SA626HA | sa62 6ha | sa626ha | Pembrokeshire | Sir Benfro | Keeston WwTW | 2002 | 1195 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.27 | 11.88 | 13.13 | 189405 | 220100 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HB | SA626HB | sa62 6hb | sa626hb | Pembrokeshire | Sir Benfro | Keeston WwTW | 2941 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 189569 | 221342 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HF | SA626HF | sa62 6hf | sa626hf | Pembrokeshire | Sir Benfro | Camrose WwTW | 3165 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 189970 | 221942 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HG | SA626HG | sa62 6hg | sa626hg | Pembrokeshire | Sir Benfro | Camrose WwTW | 2002 | 1230 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.93 | 12.23 | 13.51 | 191348 | 221678 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HH | SA626HH | sa62 6hh | sa626hh | Pembrokeshire | Sir Benfro | Camrose WwTW | 316 | 1207 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.5 | 12 | 13.26 | 192269 | 220255 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HJ | SA626HJ | sa62 6hj | sa626hj | Pembrokeshire | Sir Benfro | Camrose WwTW | 2034 | 1215 | 1200to1500 | 2.43 | 1.78 | 1.3 | 22.65 | 12.08 | 13.35 | 190704 | 220996 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HL | SA626HL | sa62 6hl | sa626hl | Pembrokeshire | Sir Benfro | Keeston WwTW | 1281 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 190097 | 219739 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HN | SA626HN | sa62 6hn | sa626hn | Pembrokeshire | Sir Benfro | Keeston WwTW | 1131 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 191142 | 219761 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HP | SA626HP | sa62 6hp | sa626hp | Pembrokeshire | Sir Benfro | Camrose WwTW | 2373 | 1180 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.99 | 11.73 | 12.96 | 193113 | 217747 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HQ | SA626HQ | sa62 6hq | sa626hq | Pembrokeshire | Sir Benfro | Camrose WwTW | 1409 | 1216 | 1200to1500 | 2.43 | 1.78 | 1.31 | 22.66 | 12.09 | 13.36 | 191585 | 221112 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HR | SA626HR | sa62 6hr | sa626hr | Pembrokeshire | Sir Benfro | Keeston WwTW | 3046 | 1210 | 1200to1500 | 2.42 | 1.77 | 1.3 | 22.55 | 12.03 | 13.29 | 189671 | 221501 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HT | SA626HT | sa62 6ht | sa626ht | Pembrokeshire | Sir Benfro | Camrose WwTW | 3250 | 1179 | 900to1200 | 2.36 | 1.73 | 1.27 | 21.97 | 11.72 | 12.95 | 194710 | 217656 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HU | SA626HU | sa62 6hu | sa626hu | Pembrokeshire | Sir Benfro | Camrose WwTW | 2473 | 1169 | 900to1200 | 2.34 | 1.71 | 1.26 | 21.79 | 11.62 | 12.84 | 194148 | 218196 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HW | SA626HW | sa62 6hw | sa626hw | Pembrokeshire | Sir Benfro | Camrose WwTW | 1353 | 1196 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.29 | 11.89 | 13.14 | 193127 | 218841 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HX | SA626HX | sa62 6hx | sa626hx | Pembrokeshire | Sir Benfro | Camrose WwTW | 1746 | 1182 | 900to1200 | 2.37 | 1.73 | 1.27 | 22.03 | 11.75 | 12.99 | 193925 | 219031 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HY | SA626HY | sa62 6hy | sa626hy | Pembrokeshire | Sir Benfro | Camrose WwTW | 1463 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 193943 | 219797 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6HZ | SA626HZ | sa62 6hz | sa626hz | Pembrokeshire | Sir Benfro | Camrose WwTW | 1079 | 1193 | 900to1200 | 2.39 | 1.75 | 1.28 | 22.24 | 11.86 | 13.11 | 193573 | 220153 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JA | SA626JA | sa62 6ja | sa626ja | Pembrokeshire | Sir Benfro | Camrose WwTW | 349 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 192844 | 220098 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JB | SA626JB | sa62 6jb | sa626jb | Pembrokeshire | Sir Benfro | Camrose WwTW | 321 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 192698 | 219787 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JD | SA626JD | sa62 6jd | sa626jd | Pembrokeshire | Sir Benfro | Camrose WwTW | 246 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 192709 | 220170 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JE | SA626JE | sa62 6je | sa626je | Pembrokeshire | Sir Benfro | Camrose WwTW | 159 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 192634 | 220126 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JF | SA626JF | sa62 6jf | sa626jf | Pembrokeshire | Sir Benfro | Camrose WwTW | 435 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 192783 | 220371 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JG | SA626JG | sa62 6jg | sa626jg | Pembrokeshire | Sir Benfro | Camrose WwTW | 656 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 192785 | 220631 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JH | SA626JH | sa62 6jh | sa626jh | Pembrokeshire | Sir Benfro | Camrose WwTW | 1407 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 193169 | 221278 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JJ | SA626JJ | sa62 6jj | sa626jj | Pembrokeshire | Sir Benfro | Camrose WwTW | 1680 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 193253 | 221542 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JL | SA626JL | sa62 6jl | sa626jl | Pembrokeshire | Sir Benfro | Treffgarne STW | 1884 | 1268 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.63 | 12.6 | 13.93 | 194015 | 222524 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JN | SA626JN | sa62 6jn | sa626jn | Pembrokeshire | Sir Benfro | Treffgarne STW | 2135 | 1226 | 1200to1500 | 2.45 | 1.8 | 1.32 | 22.85 | 12.19 | 13.47 | 194130 | 221685 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JP | SA626JP | sa62 6jp | sa626jp | Pembrokeshire | Sir Benfro | Camrose WwTW | 2698 | 1269 | 1200to1500 | 2.54 | 1.86 | 1.36 | 23.65 | 12.61 | 13.94 | 192480 | 222738 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JQ | SA626JQ | sa62 6jq | sa626jq | Pembrokeshire | Sir Benfro | Camrose WwTW | 1004 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 192860 | 220977 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JR | SA626JR | sa62 6jr | sa626jr | Pembrokeshire | Sir Benfro | Camrose WwTW | 554 | 1204 | 1200to1500 | 2.41 | 1.76 | 1.29 | 22.44 | 11.97 | 13.23 | 192813 | 220497 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JS | SA626JS | sa62 6js | sa626js | Pembrokeshire | Sir Benfro | Camrose WwTW | 652 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 192731 | 220650 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6JW | SA626JW | sa62 6jw | sa626jw | Pembrokeshire | Sir Benfro | Camrose WwTW | 1509 | 1227 | 1200to1500 | 2.46 | 1.8 | 1.32 | 22.87 | 12.2 | 13.48 | 192535 | 221549 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA62 6LF | SA626LF | sa62 6lf | sa626lf | Pembrokeshire | Sir Benfro | Camrose WwTW | 572 | 1200 | 1200to1500 | 2.4 | 1.76 | 1.29 | 22.37 | 11.93 | 13.18 | 192746 | 220556 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4AA | SA634AA | sa63 4aa | sa634aa | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 711 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201807 | 220939 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4AB | SA634AB | sa63 4ab | sa634ab | Pembrokeshire | Sir Benfro | Walton East STW | 810 | 1378 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.68 | 13.7 | 15.14 | 201575 | 222638 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4AD | SA634AD | sa63 4ad | sa634ad | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 450 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201535 | 220869 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4QH | SA634QH | sa63 4qh | sa634qh | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 696 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201771 | 221135 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4QJ | SA634QJ | sa63 4qj | sa634qj | Pembrokeshire | Sir Benfro | Walton East STW | 1085 | 1358 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.31 | 13.5 | 14.92 | 201857 | 222010 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4QL | SA634QL | sa63 4ql | sa634ql | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 1168 | 1341 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.99 | 13.33 | 14.73 | 201047 | 222134 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4QP | SA634QP | sa63 4qp | sa634qp | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 647 | 1288 | 1200to1500 | 2.58 | 1.89 | 1.38 | 24.01 | 12.8 | 14.15 | 200452 | 220901 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4QR | SA634QR | sa63 4qr | sa634qr | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 1147 | 1303 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.29 | 12.95 | 14.32 | 200132 | 220346 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4QS | SA634QS | sa63 4qs | sa634qs | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 662 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 200598 | 220531 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4QT | SA634QT | sa63 4qt | sa634qt | Pembrokeshire | Sir Benfro | Walton East STW | 1606 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 203515 | 221949 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4QU | SA634QU | sa63 4qu | sa634qu | Pembrokeshire | Sir Benfro | Walton East STW | 2872 | 1377 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.67 | 13.69 | 15.13 | 204622 | 221309 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4QX | SA634QX | sa63 4qx | sa634qx | Pembrokeshire | Sir Benfro | Walton East STW | 3139 | 1377 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.67 | 13.69 | 15.13 | 204841 | 221156 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4QY | SA634QY | sa63 4qy | sa634qy | Pembrokeshire | Sir Benfro | Llys Y Fran WwTW | 3094 | 1377 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.67 | 13.69 | 15.13 | 204944 | 221325 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4QZ | SA634QZ | sa63 4qz | sa634qz | Pembrokeshire | Sir Benfro | Llawhaden STW | 3344 | 1377 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.67 | 13.69 | 15.13 | 205477 | 220671 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RA | SA634RA | sa63 4ra | sa634ra | Pembrokeshire | Sir Benfro | Llys Y Fran WwTW | 2885 | 1389 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.89 | 13.81 | 15.26 | 204979 | 221567 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RB | SA634RB | sa63 4rb | sa634rb | Pembrokeshire | Sir Benfro | Llys Y Fran WwTW | 2255 | 1389 | 1200to1500 | 2.78 | 2.03 | 1.49 | 25.89 | 13.81 | 15.26 | 204988 | 222286 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RD | SA634RD | sa63 4rd | sa634rd | Pembrokeshire | Sir Benfro | Llys Y Fran WwTW | 2128 | 1393 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.96 | 13.85 | 15.3 | 205754 | 223383 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RE | SA634RE | sa63 4re | sa634re | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 1822 | 1484 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.66 | 14.75 | 16.3 | 205786 | 224241 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RG | SA634RG | sa63 4rg | sa634rg | Pembrokeshire | Sir Benfro | Maenclochog STW | 2028 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 206294 | 225263 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RH | SA634RH | sa63 4rh | sa634rh | Pembrokeshire | Sir Benfro | Maenclochog STW | 1916 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 206244 | 225452 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RJ | SA634RJ | sa63 4rj | sa634rj | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 1168 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 205043 | 225125 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RL | SA634RL | sa63 4rl | sa634rl | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 943 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 204884 | 224928 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RN | SA634RN | sa63 4rn | sa634rn | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 1359 | 1591 | Over1500 | 3.18 | 2.33 | 1.71 | 29.65 | 15.82 | 17.48 | 204850 | 225661 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RP | SA634RP | sa63 4rp | sa634rp | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 807 | 1510 | Over1500 | 3.02 | 2.21 | 1.62 | 28.14 | 15.01 | 16.59 | 204786 | 224781 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RQ | SA634RQ | sa63 4rq | sa634rq | Pembrokeshire | Sir Benfro | Maenclochog STW | 1801 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 206378 | 225487 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RR | SA634RR | sa63 4rr | sa634rr | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 327 | 1482 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.62 | 14.73 | 16.28 | 204326 | 224624 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RS | SA634RS | sa63 4rs | sa634rs | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 298 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 204116 | 224325 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RT | SA634RT | sa63 4rt | sa634rt | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 690 | 1458 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.17 | 14.49 | 16.02 | 204675 | 224456 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RU | SA634RU | sa63 4ru | sa634ru | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 1615 | 1591 | Over1500 | 3.18 | 2.33 | 1.71 | 29.65 | 15.82 | 17.48 | 205239 | 225636 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RX | SA634RX | sa63 4rx | sa634rx | Pembrokeshire | Sir Benfro | Maenclochog STW | 1866 | 1620 | Over1500 | 3.24 | 2.37 | 1.74 | 30.19 | 16.1 | 17.8 | 205777 | 226247 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4RY | SA634RY | sa63 4ry | sa634ry | Pembrokeshire | Sir Benfro | Maenclochog STW | 1224 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 206960 | 225786 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SA | SA634SA | sa63 4sa | sa634sa | Pembrokeshire | Sir Benfro | Maenclochog STW | 1839 | 1523 | Over1500 | 3.05 | 2.23 | 1.64 | 28.39 | 15.14 | 16.73 | 207080 | 225085 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SB | SA634SB | sa63 4sb | sa634sb | Pembrokeshire | Sir Benfro | Maenclochog STW | 2426 | 1454 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.1 | 14.45 | 15.97 | 207592 | 224440 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SD | SA634SD | sa63 4sd | sa634sd | Pembrokeshire | Sir Benfro | Llys Y Fran WwTW | 3635 | 1364 | 1200to1500 | 2.73 | 2 | 1.46 | 25.42 | 13.56 | 14.99 | 206888 | 222297 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SE | SA634SE | sa63 4se | sa634se | Pembrokeshire | Sir Benfro | Llawhaden STW | 3628 | 1342 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.01 | 13.34 | 14.74 | 206956 | 221225 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SF | SA634SF | sa63 4sf | sa634sf | Pembrokeshire | Sir Benfro | Llawhaden STW | 3122 | 1342 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.01 | 13.34 | 14.74 | 207417 | 220661 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SG | SA634SG | sa63 4sg | sa634sg | Pembrokeshire | Sir Benfro | Llys Y Fran WwTW | 3491 | 1384 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.8 | 13.76 | 15.21 | 206117 | 221595 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SJ | SA634SJ | sa63 4sj | sa634sj | Pembrokeshire | Sir Benfro | Walton East STW | 474 | 1378 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.68 | 13.7 | 15.14 | 202385 | 223466 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SL | SA634SL | sa63 4sl | sa634sl | Pembrokeshire | Sir Benfro | Walton East STW | 1437 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 203037 | 221766 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SN | SA634SN | sa63 4sn | sa634sn | Pembrokeshire | Sir Benfro | Walton East STW | 1703 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 203669 | 221986 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SP | SA634SP | sa63 4sp | sa634sp | Pembrokeshire | Sir Benfro | Llys Y Fran WwTW | 2136 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 204407 | 222151 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SR | SA634SR | sa63 4sr | sa634sr | Pembrokeshire | Sir Benfro | Walton East STW | 1517 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 203782 | 222677 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SS | SA634SS | sa63 4ss | sa634ss | Pembrokeshire | Sir Benfro | Llys Y Fran WwTW | 703 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 204113 | 223572 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4ST | SA634ST | sa63 4st | sa634st | Pembrokeshire | Sir Benfro | Llys Y Fran WwTW | 1197 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 203764 | 222998 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SU | SA634SU | sa63 4su | sa634su | Pembrokeshire | Sir Benfro | Walton East STW | 380 | 1378 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.68 | 13.7 | 15.14 | 202303 | 223380 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SW | SA634SW | sa63 4sw | sa634sw | Pembrokeshire | Sir Benfro | Walton East STW | 309 | 1378 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.68 | 13.7 | 15.14 | 202194 | 223290 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SX | SA634SX | sa63 4sx | sa634sx | Pembrokeshire | Sir Benfro | Walton East STW | 547 | 1378 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.68 | 13.7 | 15.14 | 201943 | 223414 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4SY | SA634SY | sa63 4sy | sa634sy | Pembrokeshire | Sir Benfro | Walton East STW | 349 | 1378 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.68 | 13.7 | 15.14 | 202135 | 222692 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TA | SA634TA | sa63 4ta | sa634ta | Pembrokeshire | Sir Benfro | Walton East STW | 694 | 1416 | 1200to1500 | 2.83 | 2.07 | 1.52 | 26.39 | 14.08 | 15.56 | 202003 | 223627 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TB | SA634TB | sa63 4tb | sa634tb | Pembrokeshire | Sir Benfro | Ambleston STW | 1447 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 201725 | 224733 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TD | SA634TD | sa63 4td | sa634td | Pembrokeshire | Sir Benfro | Ambleston STW | 1226 | 1461 | 1200to1500 | 2.92 | 2.14 | 1.57 | 27.23 | 14.52 | 16.05 | 201596 | 225206 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TE | SA634TE | sa63 4te | sa634te | Pembrokeshire | Sir Benfro | Ambleston STW | 1805 | 1528 | Over1500 | 3.06 | 2.24 | 1.64 | 28.48 | 15.19 | 16.79 | 202124 | 225668 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TG | SA634TG | sa63 4tg | sa634tg | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 1711 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 202958 | 225957 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TH | SA634TH | sa63 4th | sa634th | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 2244 | 1529 | Over1500 | 3.06 | 2.24 | 1.64 | 28.5 | 15.2 | 16.8 | 202668 | 226406 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TJ | SA634TJ | sa63 4tj | sa634tj | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 2580 | 1542 | Over1500 | 3.09 | 2.26 | 1.66 | 28.74 | 15.33 | 16.94 | 202820 | 226894 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TL | SA634TL | sa63 4tl | sa634tl | Pembrokeshire | Sir Benfro | Ambleston STW | 2282 | 1515 | Over1500 | 3.03 | 2.22 | 1.63 | 28.24 | 15.06 | 16.65 | 201985 | 226853 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TN | SA634TN | sa63 4tn | sa634tn | Pembrokeshire | Sir Benfro | Ambleston STW | 1468 | 1503 | Over1500 | 3.01 | 2.2 | 1.61 | 28.01 | 14.94 | 16.51 | 200984 | 226574 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TP | SA634TP | sa63 4tp | sa634tp | Pembrokeshire | Sir Benfro | Puncheston WwTW | 2019 | 1476 | 1200to1500 | 2.95 | 2.16 | 1.59 | 27.51 | 14.67 | 16.22 | 200822 | 227817 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TR | SA634TR | sa63 4tr | sa634tr | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 2565 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 203742 | 227152 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TS | SA634TS | sa63 4ts | sa634ts | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 2682 | 1614 | Over1500 | 3.23 | 2.36 | 1.73 | 30.08 | 16.04 | 17.73 | 204851 | 227144 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TT | SA634TT | sa63 4tt | sa634tt | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 2934 | 1581 | Over1500 | 3.16 | 2.32 | 1.7 | 29.47 | 15.72 | 17.37 | 204445 | 227500 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TU | SA634TU | sa63 4tu | sa634tu | Pembrokeshire | Sir Benfro | Puncheston WwTW | 3441 | 1580 | Over1500 | 3.16 | 2.31 | 1.7 | 29.45 | 15.71 | 17.36 | 203987 | 228156 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TX | SA634TX | sa63 4tx | sa634tx | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 3173 | 1554 | Over1500 | 3.11 | 2.28 | 1.67 | 28.96 | 15.45 | 17.07 | 203384 | 227713 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4TY | SA634TY | sa63 4ty | sa634ty | Pembrokeshire | Sir Benfro | Rosebush WwTW | 3178 | 1580 | Over1500 | 3.16 | 2.31 | 1.7 | 29.45 | 15.71 | 17.36 | 204247 | 228395 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA63 4UA | SA634UA | sa63 4ua | sa634ua | Pembrokeshire | Sir Benfro | Rosebush WwTW | 2173 | 1619 | Over1500 | 3.24 | 2.37 | 1.74 | 30.18 | 16.09 | 17.79 | 205461 | 228061 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UB | SA634UB | sa63 4ub | sa634ub | Pembrokeshire | Sir Benfro | Rosebush WwTW | 2913 | 1679 | Over1500 | 3.36 | 2.46 | 1.8 | 31.29 | 16.69 | 18.45 | 204433 | 228857 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA63 4UD | SA634UD | sa63 4ud | sa634ud | Pembrokeshire | Sir Benfro | Puncheston WwTW | 2641 | 1641 | Over1500 | 3.28 | 2.4 | 1.76 | 30.59 | 16.31 | 18.03 | 203420 | 228818 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA63 4UE | SA634UE | sa63 4ue | sa634ue | Pembrokeshire | Sir Benfro | Puncheston WwTW | 1765 | 1502 | Over1500 | 3.01 | 2.2 | 1.61 | 27.99 | 14.93 | 16.5 | 201901 | 228324 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UG | SA634UG | sa63 4ug | sa634ug | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 710 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201665 | 220542 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UH | SA634UH | sa63 4uh | sa634uh | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 604 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201700 | 220967 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UJ | SA634UJ | sa63 4uj | sa634uj | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 646 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201742 | 220987 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UL | SA634UL | sa63 4ul | sa634ul | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 710 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201804 | 221024 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UN | SA634UN | sa63 4un | sa634un | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 387 | 1325 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.7 | 13.17 | 14.56 | 201472 | 220877 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UP | SA634UP | sa63 4up | sa634up | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 539 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201630 | 220891 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UR | SA634UR | sa63 4ur | sa634ur | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 563 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201652 | 220879 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UT | SA634UT | sa63 4ut | sa634ut | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 608 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201695 | 220861 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UU | SA634UU | sa63 4uu | sa634uu | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 752 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201803 | 220711 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UW | SA634UW | sa63 4uw | sa634uw | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 507 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201595 | 220877 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UX | SA634UX | sa63 4ux | sa634ux | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 742 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201719 | 220564 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UY | SA634UY | sa63 4uy | sa634uy | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 736 | 1305 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.32 | 12.97 | 14.34 | 201015 | 220235 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4UZ | SA634UZ | sa63 4uz | sa634uz | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 770 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201841 | 220773 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4WA | SA634WA | sa63 4wa | sa634wa | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 620 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 201692 | 220796 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4XA | SA634XA | sa63 4xa | sa634xa | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 1056 | 1315 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.51 | 13.07 | 14.45 | 201867 | 220246 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4XB | SA634XB | sa63 4xb | sa634xb | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 1450 | 1315 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.51 | 13.07 | 14.45 | 202011 | 219842 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4XD | SA634XD | sa63 4xd | sa634xd | Pembrokeshire | Sir Benfro | Clarbeston WwTW | 1686 | 1316 | 1200to1500 | 2.63 | 1.93 | 1.41 | 24.53 | 13.08 | 14.46 | 202678 | 220385 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4XE | SA634XE | sa63 4xe | sa634xe | Pembrokeshire | Sir Benfro | Wiston STW | 2574 | 1345 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.07 | 13.37 | 14.78 | 204008 | 219878 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4XG | SA634XG | sa63 4xg | sa634xg | Pembrokeshire | Sir Benfro | Llawhaden STW | 2772 | 1354 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.24 | 13.46 | 14.88 | 205024 | 219728 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA63 4XH | SA634XH | sa63 4xh | sa634xh | Pembrokeshire | Sir Benfro | Llawhaden STW | 3221 | 1354 | 1200to1500 | 2.71 | 1.98 | 1.45 | 25.24 | 13.46 | 14.88 | 204817 | 220138 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9QB | SA659QB | sa65 9qb | sa659qb | Pembrokeshire | Sir Benfro | Panteg STW | 293 | 1149 | 900to1200 | 2.3 | 1.68 | 1.23 | 21.42 | 11.42 | 12.62 | 192510 | 234844 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9QD | SA659QD | sa65 9qd | sa659qd | Pembrokeshire | Sir Benfro | Panteg STW | 431 | 1186 | 900to1200 | 2.37 | 1.74 | 1.27 | 22.11 | 11.79 | 13.03 | 192376 | 234722 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9QT | SA659QT | sa65 9qt | sa659qt | Pembrokeshire | Sir Benfro | Panteg STW | 2338 | 1258 | 1200to1500 | 2.52 | 1.84 | 1.35 | 23.45 | 12.51 | 13.82 | 195137 | 234862 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9QU | SA659QU | sa65 9qu | sa659qu | Pembrokeshire | Sir Benfro | Panteg STW | 1629 | 1250 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.3 | 12.43 | 13.73 | 194367 | 234355 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9QX | SA659QX | sa65 9qx | sa659qx | Pembrokeshire | Sir Benfro | Panteg STW | 1741 | 1250 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.3 | 12.43 | 13.73 | 194447 | 234236 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9QY | SA659QY | sa65 9qy | sa659qy | Pembrokeshire | Sir Benfro | Panteg STW | 1715 | 1250 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.3 | 12.43 | 13.73 | 194403 | 234190 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9QZ | SA659QZ | sa65 9qz | sa659qz | Pembrokeshire | Sir Benfro | Panteg STW | 1549 | 1250 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.3 | 12.43 | 13.73 | 194275 | 234326 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RA | SA659RA | sa65 9ra | sa659ra | Pembrokeshire | Sir Benfro | Panteg STW | 1700 | 1250 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.3 | 12.43 | 13.73 | 194338 | 234076 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RB | SA659RB | sa65 9rb | sa659rb | Pembrokeshire | Sir Benfro | Panteg STW | 1660 | 1250 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.3 | 12.43 | 13.73 | 194348 | 234199 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RD | SA659RD | sa65 9rd | sa659rd | Pembrokeshire | Sir Benfro | Panteg STW | 1519 | 1250 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.3 | 12.43 | 13.73 | 194189 | 234185 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RF | SA659RF | sa65 9rf | sa659rf | Pembrokeshire | Sir Benfro | Panteg STW | 1544 | 1250 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.3 | 12.43 | 13.73 | 194287 | 234382 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RH | SA659RH | sa65 9rh | sa659rh | Pembrokeshire | Sir Benfro | Panteg STW | 1831 | 1250 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.3 | 12.43 | 13.73 | 194483 | 234077 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RJ | SA659RJ | sa65 9rj | sa659rj | Pembrokeshire | Sir Benfro | Panteg STW | 2478 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 194629 | 233128 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RL | SA659RL | sa65 9rl | sa659rl | Pembrokeshire | Sir Benfro | Panteg STW | 2917 | 1280 | 1200to1500 | 2.56 | 1.87 | 1.37 | 23.86 | 12.72 | 14.06 | 194690 | 232578 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RN | SA659RN | sa65 9rn | sa659rn | Pembrokeshire | Sir Benfro | Panteg STW | 1891 | 1266 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.6 | 12.58 | 13.91 | 193905 | 233265 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RP | SA659RP | sa65 9rp | sa659rp | Pembrokeshire | Sir Benfro | Panteg STW | 668 | 1232 | 1200to1500 | 2.47 | 1.8 | 1.32 | 22.96 | 12.25 | 13.54 | 193377 | 234464 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RQ | SA659RQ | sa65 9rq | sa659rq | Pembrokeshire | Sir Benfro | Panteg STW | 1647 | 1250 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.3 | 12.43 | 13.73 | 194298 | 234115 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RR | SA659RR | sa65 9rr | sa659rr | Pembrokeshire | Sir Benfro | Panteg STW | 1038 | 1232 | 1200to1500 | 2.47 | 1.8 | 1.32 | 22.96 | 12.25 | 13.54 | 192889 | 233766 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RS | SA659RS | sa65 9rs | sa659rs | Pembrokeshire | Sir Benfro | Panteg STW | 1638 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 192932 | 233167 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RT | SA659RT | sa65 9rt | sa659rt | Pembrokeshire | Sir Benfro | Panteg STW | 1634 | 1255 | 1200to1500 | 2.51 | 1.84 | 1.35 | 23.39 | 12.48 | 13.79 | 192716 | 233168 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA65 9RU | SA659RU | sa65 9ru | sa659ru | Pembrokeshire | Sir Benfro | Panteg STW | 1784 | 1250 | 1200to1500 | 2.5 | 1.83 | 1.34 | 23.3 | 12.43 | 13.73 | 194396 | 234002 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7AD | SA667AD | sa66 7ad | sa667ad | Pembrokeshire | Sir Benfro | Maenclochog STW | 707 | 1643 | Over1500 | 3.29 | 2.41 | 1.76 | 30.62 | 16.33 | 18.05 | 208100 | 227293 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HB | SA667HB | sa66 7hb | sa667hb | Pembrokeshire | Sir Benfro | Clynderwen STW | 680 | 1342 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.01 | 13.34 | 14.74 | 212145 | 217686 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HD | SA667HD | sa66 7hd | sa667hd | Pembrokeshire | Sir Benfro | Clynderwen STW | 1355 | 1326 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.71 | 13.18 | 14.57 | 211089 | 217941 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HE | SA667HE | sa66 7he | sa667he | Pembrokeshire | Sir Benfro | Clynderwen STW | 540 | 1342 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.01 | 13.34 | 14.74 | 211852 | 218276 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HG | SA667HG | sa66 7hg | sa667hg | Pembrokeshire | Sir Benfro | Clynderwen STW | 635 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 211812 | 218583 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HH | SA667HH | sa66 7hh | sa667hh | Pembrokeshire | Sir Benfro | Clynderwen STW | 1707 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 210707 | 218604 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HL | SA667HL | sa66 7hl | sa667hl | Pembrokeshire | Sir Benfro | Clynderwen STW | 2216 | 1362 | 1200to1500 | 2.73 | 1.99 | 1.46 | 25.39 | 13.54 | 14.96 | 210452 | 219395 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HN | SA667HN | sa66 7hn | sa667hn | Pembrokeshire | Sir Benfro | Clynderwen STW | 2821 | 1362 | 1200to1500 | 2.73 | 1.99 | 1.46 | 25.39 | 13.54 | 14.96 | 209624 | 218876 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HP | SA667HP | sa66 7hp | sa667hp | Pembrokeshire | Sir Benfro | Clynderwen STW | 3660 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 209326 | 220323 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HQ | SA667HQ | sa66 7hq | sa667hq | Pembrokeshire | Sir Benfro | Clynderwen STW | 832 | 1342 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.01 | 13.34 | 14.74 | 211571 | 218466 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HR | SA667HR | sa66 7hr | sa667hr | Pembrokeshire | Sir Benfro | Llawhaden STW | 2381 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 208160 | 219554 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HS | SA667HS | sa66 7hs | sa667hs | Pembrokeshire | Sir Benfro | Llawhaden STW | 2854 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 208394 | 219967 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HT | SA667HT | sa66 7ht | sa667ht | Pembrokeshire | Sir Benfro | Llawhaden STW | 4525 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 207901 | 221989 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HU | SA667HU | sa66 7hu | sa667hu | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 4447 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 207829 | 222338 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HW | SA667HW | sa66 7hw | sa667hw | Pembrokeshire | Sir Benfro | Llawhaden STW | 2747 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 208813 | 219470 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HX | SA667HX | sa66 7hx | sa667hx | Pembrokeshire | Sir Benfro | Llys Y Fran WwTW | 4278 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 207608 | 222271 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7HY | SA667HY | sa66 7hy | sa667hy | Pembrokeshire | Sir Benfro | Llysyfran Reservoir STW | 4311 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 207707 | 222399 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JA | SA667JA | sa66 7ja | sa667ja | Pembrokeshire | Sir Benfro | Maenclochog STW | 3591 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 208358 | 223370 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JB | SA667JB | sa66 7jb | sa667jb | Pembrokeshire | Sir Benfro | Maenclochog STW | 3879 | 1392 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.94 | 13.84 | 15.29 | 208547 | 223121 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JD | SA667JD | sa66 7jd | sa667jd | Pembrokeshire | Sir Benfro | Maenclochog STW | 4356 | 1392 | 1200to1500 | 2.79 | 2.04 | 1.5 | 25.94 | 13.84 | 15.29 | 208970 | 222752 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JE | SA667JE | sa66 7je | sa667je | Pembrokeshire | Sir Benfro | Maenclochog STW | 4624 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 209924 | 222905 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JF | SA667JF | sa66 7jf | sa667jf | Pembrokeshire | Sir Benfro | Clynderwen STW | 3877 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 209796 | 221202 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JG | SA667JG | sa66 7jg | sa667jg | Pembrokeshire | Sir Benfro | Clynderwen STW | 3819 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 209526 | 220847 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JH | SA667JH | sa66 7jh | sa667jh | Pembrokeshire | Sir Benfro | Llawhaden STW | 3445 | 1313 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.47 | 13.05 | 14.43 | 209327 | 219941 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JJ | SA667JJ | sa66 7jj | sa667jj | Pembrokeshire | Sir Benfro | Clynderwen STW | 2892 | 1371 | 1200to1500 | 2.74 | 2.01 | 1.47 | 25.55 | 13.63 | 15.06 | 210740 | 220695 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JP | SA667JP | sa66 7jp | sa667jp | Pembrokeshire | Sir Benfro | Llangolman STW | 511 | 1589 | Over1500 | 3.18 | 2.33 | 1.71 | 29.62 | 15.8 | 17.46 | 213145 | 227208 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JQ | SA667JQ | sa66 7jq | sa667jq | Pembrokeshire | Sir Benfro | Llawhaden STW | 4409 | 1327 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.73 | 13.19 | 14.58 | 209146 | 221333 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JR | SA667JR | sa66 7jr | sa667jr | Pembrokeshire | Sir Benfro | Llangolman STW | 1238 | 1696 | Over1500 | 3.39 | 2.48 | 1.82 | 31.61 | 16.86 | 18.63 | 211534 | 227686 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JS | SA667JS | sa66 7js | sa667js | Pembrokeshire | Sir Benfro | Llangolman STW | 2370 | 1778 | Over1500 | 3.56 | 2.6 | 1.91 | 33.14 | 17.67 | 19.53 | 210559 | 228265 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JT | SA667JT | sa66 7jt | sa667jt | Pembrokeshire | Sir Benfro | Rosebush WwTW | 2632 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 209843 | 228391 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JU | SA667JU | sa66 7ju | sa667ju | Pembrokeshire | Sir Benfro | Rosebush WwTW | 2462 | 1670 | Over1500 | 3.34 | 2.45 | 1.79 | 31.13 | 16.6 | 18.35 | 209632 | 228299 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JX | SA667JX | sa66 7jx | sa667jx | Pembrokeshire | Sir Benfro | Maenclochog STW | 2047 | 1691 | Over1500 | 3.38 | 2.48 | 1.82 | 31.52 | 16.81 | 18.58 | 209215 | 228038 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7JY | SA667JY | sa66 7jy | sa667jy | Pembrokeshire | Sir Benfro | Maenclochog STW | 1329 | 1623 | Over1500 | 3.25 | 2.38 | 1.74 | 30.25 | 16.13 | 17.83 | 208719 | 227473 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LA | SA667LA | sa66 7la | sa667la | Pembrokeshire | Sir Benfro | Maenclochog STW | 1023 | 1643 | Over1500 | 3.29 | 2.41 | 1.76 | 30.62 | 16.33 | 18.05 | 208406 | 227406 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LB | SA667LB | sa66 7lb | sa667lb | Pembrokeshire | Sir Benfro | Maenclochog STW | 1008 | 1737 | Over1500 | 3.48 | 2.54 | 1.87 | 32.37 | 17.27 | 19.08 | 208240 | 227588 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LD | SA667LD | sa66 7ld | sa667ld | Pembrokeshire | Sir Benfro | Maenclochog STW | 1149 | 1737 | Over1500 | 3.48 | 2.54 | 1.87 | 32.37 | 17.27 | 19.08 | 208090 | 227873 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LE | SA667LE | sa66 7le | sa667le | Pembrokeshire | Sir Benfro | Maenclochog STW | 892 | 1643 | Over1500 | 3.29 | 2.41 | 1.76 | 30.62 | 16.33 | 18.05 | 208307 | 227317 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LF | SA667LF | sa66 7lf | sa667lf | Pembrokeshire | Sir Benfro | Maenclochog STW | 663 | 1643 | Over1500 | 3.29 | 2.41 | 1.76 | 30.62 | 16.33 | 18.05 | 208096 | 227223 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LG | SA667LG | sa66 7lg | sa667lg | Pembrokeshire | Sir Benfro | Maenclochog STW | 468 | 1643 | Over1500 | 3.29 | 2.41 | 1.76 | 30.62 | 16.33 | 18.05 | 207859 | 227206 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LH | SA667LH | sa66 7lh | sa667lh | Pembrokeshire | Sir Benfro | Maenclochog STW | 1612 | 1568 | Over1500 | 3.14 | 2.3 | 1.68 | 29.23 | 15.59 | 17.23 | 208671 | 225720 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LJ | SA667LJ | sa66 7lj | sa667lj | Pembrokeshire | Sir Benfro | Maenclochog STW | 3244 | 1448 | 1200to1500 | 2.9 | 2.12 | 1.56 | 26.99 | 14.39 | 15.91 | 209076 | 224010 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LL | SA667LL | sa66 7ll | sa667ll | Pembrokeshire | Sir Benfro | Maenclochog STW | 3817 | 1423 | 1200to1500 | 2.85 | 2.08 | 1.53 | 26.52 | 14.15 | 15.63 | 209628 | 223673 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LN | SA667LN | sa66 7ln | sa667ln | Pembrokeshire | Sir Benfro | Clynderwen STW | 4429 | 1324 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.68 | 13.16 | 14.55 | 210455 | 222304 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LP | SA667LP | sa66 7lp | sa667lp | Pembrokeshire | Sir Benfro | Llangolman STW | 4220 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 210529 | 223476 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LQ | SA667LQ | sa66 7lq | sa667lq | Pembrokeshire | Sir Benfro | Maenclochog STW | 327 | 1643 | Over1500 | 3.29 | 2.41 | 1.76 | 30.62 | 16.33 | 18.05 | 207752 | 227113 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LR | SA667LR | sa66 7lr | sa667lr | Pembrokeshire | Sir Benfro | Clynderwen STW | 4527 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 211210 | 222691 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LS | SA667LS | sa66 7ls | sa667ls | Pembrokeshire | Sir Benfro | Clynderwen STW | 4256 | 1373 | 1200to1500 | 2.75 | 2.01 | 1.47 | 25.59 | 13.65 | 15.08 | 210904 | 222308 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7LT | SA667LT | sa66 7lt | sa667lt | Pembrokeshire | Sir Benfro | Clynderwen STW | 3660 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 210465 | 221433 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NA | SA667NA | sa66 7na | sa667na | Pembrokeshire | Sir Benfro | Clynderwen STW | 858 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 212091 | 219124 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NB | SA667NB | sa66 7nb | sa667nb | Pembrokeshire | Sir Benfro | Clynderwen STW | 681 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 212154 | 218959 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7ND | SA667ND | sa66 7nd | sa667nd | Pembrokeshire | Sir Benfro | Clynderwen STW | 661 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 212101 | 218915 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NE | SA667NE | sa66 7ne | sa667ne | Pembrokeshire | Sir Benfro | Clynderwen STW | 776 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 212055 | 219020 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NF | SA667NF | sa66 7nf | sa667nf | Pembrokeshire | Sir Benfro | Clynderwen STW | 993 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 211966 | 219218 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NG | SA667NG | sa66 7ng | sa667ng | Pembrokeshire | Sir Benfro | Clynderwen STW | 1070 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 211948 | 219294 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NH | SA667NH | sa66 7nh | sa667nh | Pembrokeshire | Sir Benfro | Clynderwen STW | 1293 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 212077 | 219575 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NN | SA667NN | sa66 7nn | sa667nn | Pembrokeshire | Sir Benfro | Clynderwen STW | 1176 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 212078 | 219454 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NP | SA667NP | sa66 7np | sa667np | Pembrokeshire | Sir Benfro | Clynderwen STW | 1055 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 212105 | 219336 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NQ | SA667NQ | sa66 7nq | sa667nq | Pembrokeshire | Sir Benfro | Clynderwen STW | 1176 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 212010 | 219433 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NR | SA667NR | sa66 7nr | sa667nr | Pembrokeshire | Sir Benfro | Clynderwen STW | 498 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 212139 | 218750 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NS | SA667NS | sa66 7ns | sa667ns | Pembrokeshire | Sir Benfro | Clynderwen STW | 868 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 211997 | 219094 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7NW | SA667NW | sa66 7nw | sa667nw | Pembrokeshire | Sir Benfro | Clynderwen STW | 1135 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 212092 | 219415 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7QD | SA667QD | sa66 7qd | sa667qd | Pembrokeshire | Sir Benfro | Clynderwen STW | 3927 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 212083 | 222235 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7QE | SA667QE | sa66 7qe | sa667qe | Pembrokeshire | Sir Benfro | Llangolman STW | 3973 | 1360 | 1200to1500 | 2.72 | 1.99 | 1.46 | 25.35 | 13.52 | 14.94 | 211204 | 223425 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7QG | SA667QG | sa66 7qg | sa667qg | Pembrokeshire | Sir Benfro | Llangolman STW | 3498 | 1396 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26.02 | 13.88 | 15.34 | 211752 | 223746 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7QH | SA667QH | sa66 7qh | sa667qh | Pembrokeshire | Sir Benfro | Llangolman STW | 2787 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 211464 | 224603 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7QJ | SA667QJ | sa66 7qj | sa667qj | Pembrokeshire | Sir Benfro | Llangolman STW | 2656 | 1477 | 1200to1500 | 2.96 | 2.16 | 1.59 | 27.53 | 14.68 | 16.23 | 211216 | 224888 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7QL | SA667QL | sa66 7ql | sa667ql | Pembrokeshire | Sir Benfro | Llangolman STW | 1130 | 1611 | Over1500 | 3.22 | 2.36 | 1.73 | 30.03 | 16.01 | 17.7 | 211686 | 226525 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7QN | SA667QN | sa66 7qn | sa667qn | Pembrokeshire | Sir Benfro | Rosebush WwTW | 2423 | 1839 | Over1500 | 3.68 | 2.69 | 1.98 | 34.28 | 18.28 | 20.2 | 209747 | 229016 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7QP | SA667QP | sa66 7qp | sa667qp | Pembrokeshire | Sir Benfro | Rosebush WwTW | 2133 | 1848 | Over1500 | 3.7 | 2.71 | 1.98 | 34.44 | 18.37 | 20.3 | 209458 | 229303 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7QR | SA667QR | sa66 7qr | sa667qr | Pembrokeshire | Sir Benfro | Rosebush WwTW | 547 | 1876 | Over1500 | 3.75 | 2.75 | 2.01 | 34.97 | 18.65 | 20.61 | 207583 | 228686 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7QS | SA667QS | sa66 7qs | sa667qs | Pembrokeshire | Sir Benfro | Rosebush WwTW | 133 | 1800 | Over1500 | 3.6 | 2.64 | 1.93 | 33.55 | 17.89 | 19.78 | 207232 | 229080 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7QT | SA667QT | sa66 7qt | sa667qt | Pembrokeshire | Sir Benfro | Rosebush WwTW | 136 | 1800 | Over1500 | 3.6 | 2.64 | 1.93 | 33.55 | 17.89 | 19.78 | 207365 | 229302 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7QU | SA667QU | sa66 7qu | sa667qu | Pembrokeshire | Sir Benfro | Rosebush WwTW | 316 | 1876 | Over1500 | 3.75 | 2.75 | 2.01 | 34.97 | 18.65 | 20.61 | 207532 | 229413 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7QW | SA667QW | sa66 7qw | sa667qw | Pembrokeshire | Sir Benfro | Llangolman STW | 3100 | 1846 | Over1500 | 3.69 | 2.7 | 1.98 | 34.41 | 18.35 | 20.28 | 210524 | 229396 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7QX | SA667QX | sa66 7qx | sa667qx | Pembrokeshire | Sir Benfro | Rosebush WwTW | 533 | 1845 | Over1500 | 3.69 | 2.7 | 1.98 | 34.39 | 18.34 | 20.27 | 207608 | 229625 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7QY | SA667QY | sa66 7qy | sa667qy | Pembrokeshire | Sir Benfro | Rosebush WwTW | 635 | 1791 | Over1500 | 3.58 | 2.62 | 1.92 | 33.38 | 17.8 | 19.68 | 206866 | 229606 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7RA | SA667RA | sa66 7ra | sa667ra | Pembrokeshire | Sir Benfro | Rosebush WwTW | 1493 | 1767 | Over1500 | 3.54 | 2.59 | 1.9 | 32.93 | 17.56 | 19.41 | 206133 | 230065 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7RB | SA667RB | sa66 7rb | sa667rb | Pembrokeshire | Sir Benfro | Rosebush WwTW | 1849 | 1826 | Over1500 | 3.65 | 2.67 | 1.96 | 34.03 | 18.15 | 20.06 | 206626 | 230881 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7RD | SA667RD | sa66 7rd | sa667rd | Pembrokeshire | Sir Benfro | Rosebush WwTW | 2963 | 1739 | Over1500 | 3.48 | 2.55 | 1.87 | 32.41 | 17.29 | 19.11 | 204852 | 230798 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7RG | SA667RG | sa66 7rg | sa667rg | Pembrokeshire | Sir Benfro | Puncheston WwTW | 2855 | 1659 | Over1500 | 3.32 | 2.43 | 1.78 | 30.92 | 16.49 | 18.23 | 203667 | 230795 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7RH | SA667RH | sa66 7rh | sa667rh | Pembrokeshire | Sir Benfro | Rosebush WwTW | 1084 | 1728 | Over1500 | 3.46 | 2.53 | 1.86 | 32.21 | 17.18 | 18.99 | 206779 | 228237 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7RJ | SA667RJ | sa66 7rj | sa667rj | Pembrokeshire | Sir Benfro | Maenclochog STW | 943 | 1728 | Over1500 | 3.46 | 2.53 | 1.86 | 32.21 | 17.18 | 18.99 | 207261 | 227768 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7RL | SA667RL | sa66 7rl | sa667rl | Pembrokeshire | Sir Benfro | Maenclochog STW | 407 | 1662 | Over1500 | 3.33 | 2.43 | 1.78 | 30.98 | 16.52 | 18.26 | 207175 | 227052 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7RR | SA667RR | sa66 7rr | sa667rr | Carmarthenshire | Sir Gaerfyrddin | Llangolman STW | 2389 | 1626 | Over1500 | 3.25 | 2.38 | 1.75 | 30.31 | 16.16 | 17.86 | 214939 | 227781 | Carmarthenshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA66 7RS | SA667RS | sa66 7rs | sa667rs | Carmarthenshire | Sir Gaerfyrddin | Llangolman STW | 1874 | 1620 | Over1500 | 3.24 | 2.37 | 1.74 | 30.19 | 16.1 | 17.8 | 214368 | 227855 | Carmarthenshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA66 7RT | SA667RT | sa66 7rt | sa667rt | Pembrokeshire | Sir Benfro | Llangolman STW | 2046 | 1682 | Over1500 | 3.37 | 2.46 | 1.81 | 31.35 | 16.72 | 18.48 | 214064 | 228599 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7RU | SA667RU | sa66 7ru | sa667ru | Pembrokeshire | Sir Benfro | Llangolman STW | 3028 | 1665 | Over1500 | 3.33 | 2.44 | 1.79 | 31.03 | 16.55 | 18.29 | 214611 | 229429 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7RX | SA667RX | sa66 7rx | sa667rx | Pembrokeshire | Sir Benfro | Llangolman STW | 3707 | 1758 | Over1500 | 3.52 | 2.57 | 1.89 | 32.77 | 17.48 | 19.31 | 214549 | 230308 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7RY | SA667RY | sa66 7ry | sa667ry | Pembrokeshire | Sir Benfro | Llangolman STW | 4081 | 1763 | Over1500 | 3.53 | 2.58 | 1.89 | 32.86 | 17.53 | 19.37 | 214541 | 230741 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7SA | SA667SA | sa66 7sa | sa667sa | Pembrokeshire | Sir Benfro | Llangolman STW | 6367 | 1776 | Over1500 | 3.55 | 2.6 | 1.91 | 33.1 | 17.65 | 19.51 | 216104 | 232472 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7SB | SA667SB | sa66 7sb | sa667sb | Pembrokeshire | Sir Benfro | Llangolman STW | 5155 | 1812 | Over1500 | 3.63 | 2.65 | 1.95 | 33.77 | 18.01 | 19.91 | 216056 | 230991 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7SD | SA667SD | sa66 7sd | sa667sd | Pembrokeshire | Sir Benfro | Llangolman STW | 3656 | 1768 | Over1500 | 3.54 | 2.59 | 1.9 | 32.95 | 17.57 | 19.42 | 214174 | 230449 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7SE | SA667SE | sa66 7se | sa667se | Pembrokeshire | Sir Benfro | Llangolman STW | 2305 | 1682 | Over1500 | 3.37 | 2.46 | 1.81 | 31.35 | 16.72 | 18.48 | 213563 | 229242 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7SF | SA667SF | sa66 7sf | sa667sf | Pembrokeshire | Sir Benfro | Llangolman STW | 1196 | 1604 | Over1500 | 3.21 | 2.35 | 1.72 | 29.9 | 15.94 | 17.62 | 213210 | 228181 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7SG | SA667SG | sa66 7sg | sa667sg | Pembrokeshire | Sir Benfro | Llangolman STW | 721 | 1696 | Over1500 | 3.39 | 2.48 | 1.82 | 31.61 | 16.86 | 18.63 | 212238 | 227729 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7SH | SA667SH | sa66 7sh | sa667sh | Pembrokeshire | Sir Benfro | Llangolman STW | 940 | 1696 | Over1500 | 3.39 | 2.48 | 1.82 | 31.61 | 16.86 | 18.63 | 212178 | 227949 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7SJ | SA667SJ | sa66 7sj | sa667sj | Pembrokeshire | Sir Benfro | Llangolman STW | 2022 | 1811 | Over1500 | 3.62 | 2.65 | 1.95 | 33.75 | 18 | 19.9 | 211626 | 228880 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7SL | SA667SL | sa66 7sl | sa667sl | Pembrokeshire | Sir Benfro | Llangolman STW | 3668 | 1823 | Over1500 | 3.65 | 2.67 | 1.96 | 33.98 | 18.12 | 20.03 | 211429 | 230592 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7SN | SA667SN | sa66 7sn | sa667sn | Pembrokeshire | Sir Benfro | Llangolman STW | 3016 | 1806 | Over1500 | 3.61 | 2.64 | 1.94 | 33.66 | 17.95 | 19.84 | 213419 | 230044 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA66 7SS | SA667SS | sa66 7ss | sa667ss | Pembrokeshire | Sir Benfro | Clynderwen STW | 1820 | 1336 | 1200to1500 | 2.67 | 1.96 | 1.43 | 24.9 | 13.28 | 14.68 | 211676 | 219994 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7SU | SA667SU | sa66 7su | sa667su | Pembrokeshire | Sir Benfro | Clynderwen STW | 2538 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 212159 | 220848 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7SX | SA667SX | sa66 7sx | sa667sx | Pembrokeshire | Sir Benfro | Clynderwen STW | 2718 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 212318 | 221037 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7SY | SA667SY | sa66 7sy | sa667sy | Pembrokeshire | Sir Benfro | Clynderwen STW | 2970 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 212238 | 221286 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TF | SA667TF | sa66 7tf | sa667tf | Pembrokeshire | Sir Benfro | Clynderwen STW | 3188 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 212129 | 221497 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TG | SA667TG | sa66 7tg | sa667tg | Pembrokeshire | Sir Benfro | Clynderwen STW | 3411 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 212040 | 221713 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TH | SA667TH | sa66 7th | sa667th | Pembrokeshire | Sir Benfro | Clynderwen STW | 2804 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 212121 | 221111 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TJ | SA667TJ | sa66 7tj | sa667tj | Pembrokeshire | Sir Benfro | Clynderwen STW | 3010 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 211851 | 221281 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TL | SA667TL | sa66 7tl | sa667tl | Pembrokeshire | Sir Benfro | Clynderwen STW | 3417 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 211502 | 221620 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TN | SA667TN | sa66 7tn | sa667tn | Pembrokeshire | Sir Benfro | Clynderwen STW | 3618 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 211905 | 221905 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TP | SA667TP | sa66 7tp | sa667tp | Pembrokeshire | Sir Benfro | Clynderwen STW | 3469 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 212026 | 221770 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TT | SA667TT | sa66 7tt | sa667tt | Pembrokeshire | Sir Benfro | Clynderwen STW | 3857 | 1390 | 1200to1500 | 2.78 | 2.04 | 1.49 | 25.91 | 13.82 | 15.27 | 212238 | 222174 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TU | SA667TU | sa66 7tu | sa667tu | Pembrokeshire | Sir Benfro | Llangolman STW | 3846 | 1398 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.06 | 13.9 | 15.36 | 212052 | 223329 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7TY | SA667TY | sa66 7ty | sa667ty | Pembrokeshire | Sir Benfro | Llangolman STW | 3512 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 212905 | 223628 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7UA | SA667UA | sa66 7ua | sa667ua | Pembrokeshire | Sir Benfro | Llangolman STW | 3277 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 212727 | 223854 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7UB | SA667UB | sa66 7ub | sa667ub | Pembrokeshire | Sir Benfro | Llangolman STW | 2670 | 1396 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26.02 | 13.88 | 15.34 | 212436 | 224468 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7UD | SA667UD | sa66 7ud | sa667ud | Pembrokeshire | Sir Benfro | Llangolman STW | 3060 | 1396 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26.02 | 13.88 | 15.34 | 212127 | 224113 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7UE | SA667UE | sa66 7ue | sa667ue | Pembrokeshire | Sir Benfro | Clynderwen STW | 2850 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 212205 | 221164 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7UR | SA667UR | sa66 7ur | sa667ur | Pembrokeshire | Sir Benfro | Llangolman STW | 3445 | 1425 | 1200to1500 | 2.85 | 2.09 | 1.53 | 26.56 | 14.17 | 15.66 | 212932 | 223697 | Pembrokeshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7UY | SA667UY | sa66 7uy | sa667uy | Carmarthenshire | Sir Gaerfyrddin | Llangolman STW | 1879 | 1594 | Over1500 | 3.19 | 2.33 | 1.71 | 29.71 | 15.85 | 17.51 | 213602 | 225516 | Carmarthenshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA66 7XH | SA667XH | sa66 7xh | sa667xh | Carmarthenshire | Sir Gaerfyrddin | Llangolman STW | 1746 | 1567 | Over1500 | 3.14 | 2.29 | 1.68 | 29.21 | 15.58 | 17.22 | 213340 | 225530 | Carmarthenshire LPA | CA | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Gaerfyrddin | Carmarthenshire County Council
SA66 7XJ | SA667XJ | sa66 7xj | sa667xj | Pembrokeshire | Sir Benfro | Llangolman STW | 128 | 1589 | Over1500 | 3.18 | 2.33 | 1.71 | 29.62 | 15.8 | 17.46 | 212512 | 227138 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7XL | SA667XL | sa66 7xl | sa667xl | Pembrokeshire | Sir Benfro | Llangolman STW | 321 | 1611 | Over1500 | 3.22 | 2.36 | 1.73 | 30.03 | 16.01 | 17.7 | 212320 | 227152 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7XN | SA667XN | sa66 7xn | sa667xn | Pembrokeshire | Sir Benfro | Llangolman STW | 905 | 1611 | Over1500 | 3.22 | 2.36 | 1.73 | 30.03 | 16.01 | 17.7 | 211735 | 227125 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7XP | SA667XP | sa66 7xp | sa667xp | Pembrokeshire | Sir Benfro | Llangolman STW | 1279 | 1640 | Over1500 | 3.28 | 2.4 | 1.76 | 30.57 | 16.3 | 18.02 | 211363 | 227195 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7XR | SA667XR | sa66 7xr | sa667xr | Pembrokeshire | Sir Benfro | Llangolman STW | 2233 | 1664 | Over1500 | 3.33 | 2.44 | 1.79 | 31.01 | 16.54 | 18.28 | 210414 | 227304 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7XS | SA667XS | sa66 7xs | sa667xs | Pembrokeshire | Sir Benfro | Maenclochog STW | 2112 | 1664 | Over1500 | 3.33 | 2.44 | 1.79 | 31.01 | 16.54 | 18.28 | 209634 | 227119 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA66 7XT | SA667XT | sa66 7xt | sa667xt | Pembrokeshire | Sir Benfro | Maenclochog STW | 2976 | 1520 | Over1500 | 3.04 | 2.23 | 1.63 | 28.33 | 15.11 | 16.7 | 210116 | 225380 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AA | SA677AA | sa67 7aa | sa677aa | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2696 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210909 | 214880 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AB | SA677AB | sa67 7ab | sa677ab | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2619 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210818 | 214864 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AE | SA677AE | sa67 7ae | sa677ae | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2482 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210711 | 214960 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AF | SA677AF | sa67 7af | sa677af | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2578 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210821 | 214975 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AG | SA677AG | sa67 7ag | sa677ag | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2665 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210811 | 214743 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AH | SA677AH | sa67 7ah | sa677ah | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2399 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210619 | 214957 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AJ | SA677AJ | sa67 7aj | sa677aj | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2461 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210643 | 214864 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AL | SA677AL | sa67 7al | sa677al | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2443 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210633 | 214884 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AN | SA677AN | sa67 7an | sa677an | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2698 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210815 | 214678 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AP | SA677AP | sa67 7ap | sa677ap | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2746 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210853 | 214647 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AQ | SA677AQ | sa67 7aq | sa677aq | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2487 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210689 | 214899 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AR | SA677AR | sa67 7ar | sa677ar | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2773 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210913 | 214704 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AS | SA677AS | sa67 7as | sa677as | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210882 | 214716 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AT | SA677AT | sa67 7at | sa677at | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2835 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210922 | 214587 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AU | SA677AU | sa67 7au | sa677au | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2906 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210998 | 214579 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AW | SA677AW | sa67 7aw | sa677aw | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2820 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211012 | 214807 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AX | SA677AX | sa67 7ax | sa677ax | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2938 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211002 | 214520 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AY | SA677AY | sa67 7ay | sa677ay | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2887 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211050 | 214728 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7AZ | SA677AZ | sa67 7az | sa677az | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2829 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211010 | 214779 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7BA | SA677BA | sa67 7ba | sa677ba | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2821 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210883 | 214546 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7BB | SA677BB | sa67 7bb | sa677bb | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2961 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211010 | 214486 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7BD | SA677BD | sa67 7bd | sa677bd | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2926 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210961 | 214472 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7BE | SA677BE | sa67 7be | sa677be | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2910 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210921 | 214435 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7BG | SA677BG | sa67 7bg | sa677bg | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2894 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210945 | 214507 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7BH | SA677BH | sa67 7bh | sa677bh | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2859 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210888 | 214480 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7BN | SA677BN | sa67 7bn | sa677bn | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2765 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210949 | 214799 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7BQ | SA677BQ | sa67 7bq | sa677bq | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2841 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210954 | 214636 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7BT | SA677BT | sa67 7bt | sa677bt | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2798 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210997 | 214826 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7BU | SA677BU | sa67 7bu | sa677bu | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2951 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211118 | 214723 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7BZ | SA677BZ | sa67 7bz | sa677bz | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2907 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211039 | 214658 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DA | SA677DA | sa67 7da | sa677da | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2973 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211134 | 214703 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DB | SA677DB | sa67 7db | sa677db | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2906 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211020 | 214622 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DD | SA677DD | sa67 7dd | sa677dd | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2967 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211097 | 214640 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DE | SA677DE | sa67 7de | sa677de | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3000 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211133 | 214638 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DF | SA677DF | sa67 7df | sa677df | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2683 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210845 | 214770 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DG | SA677DG | sa67 7dg | sa677dg | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2792 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210967 | 214774 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DY | SA677DY | sa67 7dy | sa677dy | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3072 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211229 | 214673 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7DZ | SA677DZ | sa67 7dz | sa677dz | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2976 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211051 | 214530 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7EB | SA677EB | sa67 7eb | sa677eb | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3150 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211293 | 214626 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7ED | SA677ED | sa67 7ed | sa677ed | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2823 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210970 | 214707 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7EE | SA677EE | sa67 7ee | sa677ee | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2486 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210764 | 215084 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7EF | SA677EF | sa67 7ef | sa677ef | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2481 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210808 | 215232 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7EP | SA677EP | sa67 7ep | sa677ep | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2621 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210891 | 215038 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7ET | SA677ET | sa67 7et | sa677et | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2531 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210908 | 215422 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7EX | SA677EX | sa67 7ex | sa677ex | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2430 | 1395 | 1200to1500 | 2.79 | 2.04 | 1.5 | 26 | 13.87 | 15.33 | 210851 | 216149 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7EY | SA677EY | sa67 7ey | sa677ey | Pembrokeshire | Sir Benfro | Clynderwen STW | 1680 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 211388 | 216971 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7EZ | SA677EZ | sa67 7ez | sa677ez | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2536 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210845 | 215166 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7FF | SA677FF | sa67 7ff | sa677ff | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2555 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210832 | 215069 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7FN | SA677FN | sa67 7fn | sa677fn | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2423 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210757 | 215264 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7FP | SA677FP | sa67 7fp | sa677fp | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2651 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210818 | 214788 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7PA | SA677PA | sa67 7pa | sa677pa | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 236 | 1365 | 1200to1500 | 2.73 | 2 | 1.47 | 25.44 | 13.57 | 15 | 214418 | 216941 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7PB | SA677PB | sa67 7pb | sa677pb | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 742 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 214943 | 216714 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7PL | SA677PL | sa67 7pl | sa677pl | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 816 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 215013 | 216684 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7UH | SA677UH | sa67 7uh | sa677uh | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2354 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210536 | 214887 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7UJ | SA677UJ | sa67 7uj | sa677uj | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2284 | 1356 | 1200to1500 | 2.71 | 1.99 | 1.46 | 25.27 | 13.48 | 14.9 | 210445 | 214864 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7UL | SA677UL | sa67 7ul | sa677ul | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2365 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210513 | 214820 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7UN | SA677UN | sa67 7un | sa677un | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2280 | 1356 | 1200to1500 | 2.71 | 1.99 | 1.46 | 25.27 | 13.48 | 14.9 | 210499 | 214981 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7UP | SA677UP | sa67 7up | sa677up | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2426 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210606 | 214867 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 7UW | SA677UW | sa67 7uw | sa677uw | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2481 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210588 | 214716 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8AQ | SA678AQ | sa67 8aq | sa678aq | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 198 | 1349 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.14 | 13.41 | 14.82 | 208493 | 215752 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8BS | SA678BS | sa67 8bs | sa678bs | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2284 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 209803 | 214115 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8BT | SA678BT | sa67 8bt | sa678bt | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 1363 | 1356 | 1200to1500 | 2.71 | 1.99 | 1.46 | 25.27 | 13.48 | 14.9 | 207718 | 214778 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8BU | SA678BU | sa67 8bu | sa678bu | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2874 | 1369 | 1200to1500 | 2.74 | 2 | 1.47 | 25.52 | 13.61 | 15.04 | 210280 | 213740 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8BX | SA678BX | sa67 8bx | sa678bx | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3150 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 209641 | 213032 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DE | SA678DE | sa67 8de | sa678de | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2755 | 1343 | 1200to1500 | 2.69 | 1.97 | 1.44 | 25.03 | 13.35 | 14.76 | 207198 | 213476 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DF | SA678DF | sa67 8df | sa678df | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 1884 | 1350 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.16 | 13.42 | 14.83 | 206833 | 214941 | Pembrokeshire Coast National Park LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Parc Cenedlaethol Arfordir Penfro | Pembrokeshire Coast National Park
SA67 8DG | SA678DG | sa67 8dg | sa678dg | Pembrokeshire | Sir Benfro | Llawhaden STW | 1298 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 206709 | 216305 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DH | SA678DH | sa67 8dh | sa678dh | Pembrokeshire | Sir Benfro | Llawhaden STW | 724 | 1285 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.95 | 12.77 | 14.12 | 207398 | 217191 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DJ | SA678DJ | sa67 8dj | sa678dj | Pembrokeshire | Sir Benfro | Llawhaden STW | 775 | 1286 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.97 | 12.78 | 14.13 | 207537 | 217841 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DL | SA678DL | sa67 8dl | sa678dl | Pembrokeshire | Sir Benfro | Llawhaden STW | 2162 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 207778 | 219528 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DN | SA678DN | sa67 8dn | sa678dn | Pembrokeshire | Sir Benfro | Llawhaden STW | 1869 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 206502 | 219445 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DP | SA678DP | sa67 8dp | sa678dp | Pembrokeshire | Sir Benfro | Llawhaden STW | 1213 | 1319 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.58 | 13.11 | 14.49 | 206696 | 218809 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DR | SA678DR | sa67 8dr | sa678dr | Pembrokeshire | Sir Benfro | Llawhaden STW | 976 | 1330 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.79 | 13.22 | 14.61 | 205934 | 218050 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DS | SA678DS | sa67 8ds | sa678ds | Pembrokeshire | Sir Benfro | Llawhaden STW | 606 | 1330 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.79 | 13.22 | 14.61 | 206226 | 217795 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DT | SA678DT | sa67 8dt | sa678dt | Pembrokeshire | Sir Benfro | Llawhaden STW | 1415 | 1330 | 1200to1500 | 2.66 | 1.95 | 1.43 | 24.79 | 13.22 | 14.61 | 205527 | 218218 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DU | SA678DU | sa67 8du | sa678du | Pembrokeshire | Sir Benfro | Llawhaden STW | 1730 | 1271 | 1200to1500 | 2.54 | 1.86 | 1.37 | 23.69 | 12.63 | 13.96 | 205095 | 217306 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DX | SA678DX | sa67 8dx | sa678dx | Pembrokeshire | Sir Benfro | Llawhaden STW | 1118 | 1283 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.91 | 12.75 | 14.1 | 205714 | 217336 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8DY | SA678DY | sa67 8dy | sa678dy | Pembrokeshire | Sir Benfro | Wiston STW | 1857 | 1294 | 1200to1500 | 2.59 | 1.9 | 1.39 | 24.12 | 12.86 | 14.22 | 204407 | 217204 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8EA | SA678EA | sa67 8ea | sa678ea | Pembrokeshire | Sir Benfro | Llawhaden STW | 2538 | 1300 | 1200to1500 | 2.6 | 1.9 | 1.4 | 24.23 | 12.92 | 14.28 | 204987 | 215824 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8EB | SA678EB | sa67 8eb | sa678eb | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2156 | 1314 | 1200to1500 | 2.63 | 1.92 | 1.41 | 24.49 | 13.06 | 14.44 | 206358 | 215345 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8ED | SA678ED | sa67 8ed | sa678ed | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 1670 | 1328 | 1200to1500 | 2.66 | 1.94 | 1.43 | 24.75 | 13.2 | 14.59 | 206791 | 215620 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8EH | SA678EH | sa67 8eh | sa678eh | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 1830 | 1356 | 1200to1500 | 2.71 | 1.99 | 1.46 | 25.27 | 13.48 | 14.9 | 210049 | 215087 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8EJ | SA678EJ | sa67 8ej | sa678ej | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 689 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 209044 | 215627 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8EL | SA678EL | sa67 8el | sa678el | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 244 | 1349 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.14 | 13.41 | 14.82 | 208450 | 215697 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8EN | SA678EN | sa67 8en | sa678en | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 299 | 1349 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.14 | 13.41 | 14.82 | 208323 | 215661 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8EP | SA678EP | sa67 8ep | sa678ep | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 1101 | 1356 | 1200to1500 | 2.71 | 1.99 | 1.46 | 25.27 | 13.48 | 14.9 | 207546 | 215284 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8ER | SA678ER | sa67 8er | sa678er | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 147 | 1349 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.14 | 13.41 | 14.82 | 208405 | 215795 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8ES | SA678ES | sa67 8es | sa678es | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 67 | 1349 | 1200to1500 | 2.7 | 1.98 | 1.45 | 25.14 | 13.41 | 14.82 | 208385 | 215890 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8ET | SA678ET | sa67 8et | sa678et | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 884 | 1302 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.27 | 12.94 | 14.3 | 207754 | 216510 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8EU | SA678EU | sa67 8eu | sa678eu | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 248 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 208599 | 215758 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8EX | SA678EX | sa67 8ex | sa678ex | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 358 | 1376 | 1200to1500 | 2.75 | 2.02 | 1.48 | 25.65 | 13.68 | 15.12 | 208752 | 215784 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8EY | SA678EY | sa67 8ey | sa678ey | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 1221 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 209651 | 215960 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HA | SA678HA | sa67 8ha | sa678ha | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 1868 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 210298 | 215919 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HB | SA678HB | sa67 8hb | sa678hb | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 1905 | 1399 | 1200to1500 | 2.8 | 2.05 | 1.5 | 26.08 | 13.91 | 15.37 | 210262 | 216461 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HD | SA678HD | sa67 8hd | sa678hd | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 1272 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 209422 | 216737 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HE | SA678HE | sa67 8he | sa678he | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2066 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 209284 | 217821 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HF | SA678HF | sa67 8hf | sa678hf | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2083 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 209112 | 217908 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HG | SA678HG | sa67 8hg | sa678hg | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2450 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 209476 | 218156 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HH | SA678HH | sa67 8hh | sa678hh | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 1479 | 1302 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.27 | 12.94 | 14.3 | 208275 | 217411 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HJ | SA678HJ | sa67 8hj | sa678hj | Pembrokeshire | Sir Benfro | Llawhaden STW | 1056 | 1302 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.27 | 12.94 | 14.3 | 207795 | 217245 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HL | SA678HL | sa67 8hl | sa678hl | Pembrokeshire | Sir Benfro | Llawhaden STW | 414 | 1285 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.95 | 12.77 | 14.12 | 207152 | 217382 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HN | SA678HN | sa67 8hn | sa678hn | Pembrokeshire | Sir Benfro | Llawhaden STW | 265 | 1285 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.95 | 12.77 | 14.12 | 206954 | 217384 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HP | SA678HP | sa67 8hp | sa678hp | Pembrokeshire | Sir Benfro | Llawhaden STW | 149 | 1285 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.95 | 12.77 | 14.12 | 206781 | 217452 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HQ | SA678HQ | sa67 8hq | sa678hq | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2241 | 1322 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.64 | 13.14 | 14.52 | 209164 | 218057 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HR | SA678HR | sa67 8hr | sa678hr | Pembrokeshire | Sir Benfro | Llawhaden STW | 253 | 1285 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.95 | 12.77 | 14.12 | 206764 | 217350 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HS | SA678HS | sa67 8hs | sa678hs | Pembrokeshire | Sir Benfro | Llawhaden STW | 320 | 1285 | 1200to1500 | 2.57 | 1.88 | 1.38 | 23.95 | 12.77 | 14.12 | 206747 | 217284 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HT | SA678HT | sa67 8ht | sa678ht | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 1049 | 1302 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.27 | 12.94 | 14.3 | 208436 | 216989 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HU | SA678HU | sa67 8hu | sa678hu | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 963 | 1323 | 1200to1500 | 2.65 | 1.94 | 1.42 | 24.66 | 13.15 | 14.54 | 208809 | 216825 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HW | SA678HW | sa67 8hw | sa678hw | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2092 | 1337 | 1200to1500 | 2.68 | 1.96 | 1.44 | 24.92 | 13.29 | 14.69 | 209806 | 217516 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8HX | SA678HX | sa67 8hx | sa678hx | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 4109 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 213456 | 212791 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8QQ | SA678QQ | sa67 8qq | sa678qq | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 4385 | 1427 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.6 | 14.19 | 15.68 | 212358 | 212855 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8QR | SA678QR | sa67 8qr | sa678qr | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2937 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210855 | 214283 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8QS | SA678QS | sa67 8qs | sa678qs | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3026 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210890 | 214177 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8QT | SA678QT | sa67 8qt | sa678qt | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3017 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210883 | 214184 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8QU | SA678QU | sa67 8qu | sa678qu | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3076 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214144 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8QW | SA678QW | sa67 8qw | sa678qw | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3016 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210852 | 214142 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8QX | SA678QX | sa67 8qx | sa678qx | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2946 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210778 | 214161 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8QY | SA678QY | sa67 8qy | sa678qy | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2939 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210720 | 214097 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8QZ | SA678QZ | sa67 8qz | sa678qz | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3058 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210835 | 214051 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RA | SA678RA | sa67 8ra | sa678ra | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3147 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210960 | 214069 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RB | SA678RB | sa67 8rb | sa678rb | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2916 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210731 | 214149 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RD | SA678RD | sa67 8rd | sa678rd | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3433 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211254 | 213987 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RE | SA678RE | sa67 8re | sa678re | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3512 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 211034 | 213583 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RF | SA678RF | sa67 8rf | sa678rf | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3723 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 211171 | 213421 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RG | SA678RG | sa67 8rg | sa678rg | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3900 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 211088 | 213086 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RH | SA678RH | sa67 8rh | sa678rh | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 4195 | 1427 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.6 | 14.19 | 15.68 | 211562 | 213149 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RJ | SA678RJ | sa67 8rj | sa678rj | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 4067 | 1427 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.6 | 14.19 | 15.68 | 211892 | 213488 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RL | SA678RL | sa67 8rl | sa678rl | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 4409 | 1427 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.6 | 14.19 | 15.68 | 212211 | 212900 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RN | SA678RN | sa67 8rn | sa678rn | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 4226 | 1427 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.6 | 14.19 | 15.68 | 212416 | 213004 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RP | SA678RP | sa67 8rp | sa678rp | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 4421 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 212592 | 212716 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RQ | SA678RQ | sa67 8rq | sa678rq | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 4183 | 1409 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.26 | 14.01 | 15.48 | 211075 | 212699 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RR | SA678RR | sa67 8rr | sa678rr | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 4598 | 1427 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.6 | 14.19 | 15.68 | 212153 | 212718 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8RW | SA678RW | sa67 8rw | sa678rw | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 4433 | 1427 | 1200to1500 | 2.86 | 2.09 | 1.53 | 26.6 | 14.19 | 15.68 | 212333 | 212814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8SW | SA678SW | sa67 8sw | sa678sw | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 3025 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210945 | 214258 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8TB | SA678TB | sa67 8tb | sa678tb | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 3286 | 1408 | 1200to1500 | 2.82 | 2.06 | 1.51 | 26.24 | 14 | 15.47 | 212518 | 214013 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8TD | SA678TD | sa67 8td | sa678td | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 3592 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 213194 | 213385 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8TE | SA678TE | sa67 8te | sa678te | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 4056 | 1431 | 1200to1500 | 2.86 | 2.1 | 1.54 | 26.67 | 14.22 | 15.72 | 213508 | 212835 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8TF | SA678TF | sa67 8tf | sa678tf | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 4241 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 213354 | 212676 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8TG | SA678TG | sa67 8tg | sa678tg | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 4272 | 1431 | 1200to1500 | 2.86 | 2.1 | 1.54 | 26.67 | 14.22 | 15.72 | 214161 | 212558 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8TW | SA678TW | sa67 8tw | sa678tw | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 4151 | 1435 | 1200to1500 | 2.87 | 2.1 | 1.54 | 26.75 | 14.26 | 15.77 | 213397 | 212759 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 8UR | SA678UR | sa67 8ur | sa678ur | Pembrokeshire | Sir Benfro | Llanddewi Velfrey STW | 546 | 1380 | 1200to1500 | 2.76 | 2.02 | 1.48 | 25.72 | 13.72 | 15.16 | 214651 | 216508 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9AN | SA679AN | sa67 9an | sa679an | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9AQ | SA679AQ | sa67 9aq | sa679aq | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9AR | SA679AR | sa67 9ar | sa679ar | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9AT | SA679AT | sa67 9at | sa679at | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9AW | SA679AW | sa67 9aw | sa679aw | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9AX | SA679AX | sa67 9ax | sa679ax | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9AY | SA679AY | sa67 9ay | sa679ay | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9BA | SA679BA | sa67 9ba | sa679ba | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9BE | SA679BE | sa67 9be | sa679be | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9BF | SA679BF | sa67 9bf | sa679bf | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9BG | SA679BG | sa67 9bg | sa679bg | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9BH | SA679BH | sa67 9bh | sa679bh | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
SA67 9BJ | SA679BJ | sa67 9bj | sa679bj | Pembrokeshire | Sir Benfro | Robeston Wathen Housing Act Works | 2740 | 1383 | 1200to1500 | 2.77 | 2.03 | 1.49 | 25.78 | 13.75 | 15.19 | 210928 | 214814 | Pembrokeshire LPA | PE | Afonydd Cleddau a Sir Benfro Forol/ Cleddau Rivers and Pembrokshire Marine | Cyngor Sir Penfro | Pembrokeshire County Council
LL48 6AD | LL486AD | ll48 6ad | ll486ad | Gwynedd | Gwynedd | Llanfrothen STW | 691 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 261270 | 341639 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6AJ | LL486AJ | ll48 6aj | ll486aj | Gwynedd | Gwynedd | Llanfrothen STW | 717 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 261284 | 341735 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6AQ | LL486AQ | ll48 6aq | ll486aq | Gwynedd | Gwynedd | Llanfrothen STW | 698 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 261257 | 341770 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6AX | LL486AX | ll48 6ax | ll486ax | Gwynedd | Gwynedd | Llanfrothen STW | 642 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 261219 | 341658 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6AZ | LL486AZ | ll48 6az | ll486az | Gwynedd | Gwynedd | Llanfrothen STW | 706 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 261284 | 341657 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6BH | LL486BH | ll48 6bh | ll486bh | Gwynedd | Gwynedd | Llanfrothen STW | 791 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 261370 | 341625 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6BJ | LL486BJ | ll48 6bj | ll486bj | Gwynedd | Gwynedd | Llanfrothen STW | 768 | 1647 | Over1500 | 3.3 | 2.41 | 1.77 | 30.7 | 16.37 | 18.1 | 259973 | 342070 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6BQ | LL486BQ | ll48 6bq | ll486bq | Gwynedd | Gwynedd | Llanfrothen STW | 539 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 261118 | 341635 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6BX | LL486BX | ll48 6bx | ll486bx | Gwynedd | Gwynedd | Llanfrothen STW | 853 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 261430 | 341666 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6BZ | LL486BZ | ll48 6bz | ll486bz | Gwynedd | Gwynedd | Llanfrothen STW | 926 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 261499 | 341715 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6DJ | LL486DJ | ll48 6dj | ll486dj | Gwynedd | Gwynedd | Croesor STW | 1963 | 1885 | Over1500 | 3.77 | 2.76 | 2.02 | 35.13 | 18.74 | 20.71 | 263204 | 342639 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6DQ | LL486DQ | ll48 6dq | ll486dq | Gwynedd | Gwynedd | Croesor STW | 1158 | 1885 | Over1500 | 3.77 | 2.76 | 2.02 | 35.13 | 18.74 | 20.71 | 263257 | 343463 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6DS | LL486DS | ll48 6ds | ll486ds | Gwynedd | Gwynedd | Llanfrothen STW | 2034 | 1453 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.08 | 14.44 | 15.96 | 261446 | 339760 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6DT | LL486DT | ll48 6dt | ll486dt | Gwynedd | Gwynedd | Llanfrothen STW | 1921 | 1453 | 1200to1500 | 2.91 | 2.13 | 1.56 | 27.08 | 14.44 | 15.96 | 261353 | 339842 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6DU | LL486DU | ll48 6du | ll486du | Gwynedd | Gwynedd | Llanfrothen STW | 1740 | 1577 | Over1500 | 3.16 | 2.31 | 1.69 | 29.39 | 15.68 | 17.33 | 262267 | 341177 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6DX | LL486DX | ll48 6dx | ll486dx | Gwynedd | Gwynedd | Croesor STW | 2126 | 2046 | Over1500 | 4.1 | 3 | 2.2 | 38.13 | 20.34 | 22.48 | 263972 | 342705 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6DY | LL486DY | ll48 6dy | ll486dy | Gwynedd | Gwynedd | Llanfrothen STW | 1566 | 1630 | Over1500 | 3.26 | 2.39 | 1.75 | 30.38 | 16.2 | 17.91 | 262143 | 341696 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6DZ | LL486DZ | ll48 6dz | ll486dz | Gwynedd | Gwynedd | Llanfrothen STW | 1038 | 1630 | Over1500 | 3.26 | 2.39 | 1.75 | 30.38 | 16.2 | 17.91 | 261603 | 341773 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6ED | LL486ED | ll48 6ed | ll486ed | Gwynedd | Gwynedd | Prenteg STW | 3004 | 1303 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.29 | 12.95 | 14.32 | 259680 | 338331 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6HD | LL486HD | ll48 6hd | ll486hd | Gwynedd | Gwynedd | Prenteg STW | 2727 | 1348 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.12 | 13.4 | 14.81 | 260134 | 338714 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6HF | LL486HF | ll48 6hf | ll486hf | Gwynedd | Gwynedd | Prenteg STW | 2869 | 1348 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.12 | 13.4 | 14.81 | 259998 | 338528 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6HG | LL486HG | ll48 6hg | ll486hg | Gwynedd | Gwynedd | Prenteg STW | 2902 | 1303 | 1200to1500 | 2.61 | 1.91 | 1.4 | 24.29 | 12.95 | 14.32 | 259718 | 338439 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6HL | LL486HL | ll48 6hl | ll486hl | Gwynedd | Gwynedd | Prenteg STW | 2955 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 259454 | 338359 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6HN | LL486HN | ll48 6hn | ll486hn | Gwynedd | Gwynedd | Prenteg STW | 2808 | 1348 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.12 | 13.4 | 14.81 | 259566 | 338515 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6HP | LL486HP | ll48 6hp | ll486hp | Gwynedd | Gwynedd | Prenteg STW | 2627 | 1348 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.12 | 13.4 | 14.81 | 259554 | 338696 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6HR | LL486HR | ll48 6hr | ll486hr | Gwynedd | Gwynedd | Prenteg STW | 2672 | 1348 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.12 | 13.4 | 14.81 | 259839 | 338693 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6HS | LL486HS | ll48 6hs | ll486hs | Gwynedd | Gwynedd | Prenteg STW | 2762 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 259376 | 338549 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6HT | LL486HT | ll48 6ht | ll486ht | Gwynedd | Gwynedd | Prenteg STW | 3510 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 258506 | 337892 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6HU | LL486HU | ll48 6hu | ll486hu | Gwynedd | Gwynedd | Prenteg STW | 3384 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 258870 | 337954 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6HW | LL486HW | ll48 6hw | ll486hw | Gwynedd | Gwynedd | Prenteg STW | 2684 | 1321 | 1200to1500 | 2.64 | 1.93 | 1.42 | 24.62 | 13.13 | 14.51 | 259493 | 338633 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6HY | LL486HY | ll48 6hy | ll486hy | Gwynedd | Gwynedd | Prenteg STW | 3399 | 1274 | 1200to1500 | 2.55 | 1.87 | 1.37 | 23.75 | 12.66 | 14 | 259050 | 337921 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6LJ | LL486LJ | ll48 6lj | ll486lj | Gwynedd | Gwynedd | Llanfrothen STW | 933 | 1630 | Over1500 | 3.26 | 2.39 | 1.75 | 30.38 | 16.2 | 17.91 | 261512 | 341635 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6LQ | LL486LQ | ll48 6lq | ll486lq | Gwynedd | Gwynedd | Llanfrothen STW | 891 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 261450 | 341792 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6LX | LL486LX | ll48 6lx | ll486lx | Gwynedd | Gwynedd | Llanfrothen STW | 1515 | 1630 | Over1500 | 3.26 | 2.39 | 1.75 | 30.38 | 16.2 | 17.91 | 262009 | 342102 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6LZ | LL486LZ | ll48 6lz | ll486lz | Gwynedd | Gwynedd | Croesor STW | 1894 | 1885 | Over1500 | 3.77 | 2.76 | 2.02 | 35.13 | 18.74 | 20.71 | 262806 | 342705 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6RU | LL486RU | ll48 6ru | ll486ru | Gwynedd | Gwynedd | Prenteg STW | 1107 | 1382 | 1200to1500 | 2.77 | 2.02 | 1.48 | 25.76 | 13.74 | 15.18 | 259748 | 340298 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6RY | LL486RY | ll48 6ry | ll486ry | Gwynedd | Gwynedd | Prenteg STW | 2234 | 1348 | 1200to1500 | 2.7 | 1.97 | 1.45 | 25.12 | 13.4 | 14.81 | 260224 | 339276 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6SE | LL486SE | ll48 6se | ll486se | Gwynedd | Gwynedd | Llanfrothen STW | 820 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 261359 | 341855 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6SF | LL486SF | ll48 6sf | ll486sf | Gwynedd | Gwynedd | Llanfrothen STW | 847 | 1588 | Over1500 | 3.18 | 2.33 | 1.71 | 29.6 | 15.79 | 17.45 | 261377 | 341885 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6SG | LL486SG | ll48 6sg | ll486sg | Gwynedd | Gwynedd | Llanfrothen STW | 1647 | 1797 | Over1500 | 3.6 | 2.63 | 1.93 | 33.49 | 17.86 | 19.74 | 261800 | 342706 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL48 6SH | LL486SH | ll48 6sh | ll486sh | Gwynedd | Gwynedd | Croesor STW | 1891 | 1804 | Over1500 | 3.61 | 2.64 | 1.94 | 33.62 | 17.93 | 19.82 | 261415 | 343544 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6SN | LL486SN | ll48 6sn | ll486sn | Gwynedd | Gwynedd | Nantmor STW | 1866 | 1913 | Over1500 | 3.83 | 2.8 | 2.05 | 35.66 | 19.02 | 21.02 | 261427 | 345819 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6SP | LL486SP | ll48 6sp | ll486sp | Gwynedd | Gwynedd | Croesor STW | 694 | 2148 | Over1500 | 4.3 | 3.15 | 2.31 | 40.04 | 21.35 | 23.6 | 262649 | 343986 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6SR | LL486SR | ll48 6sr | ll486sr | Gwynedd | Gwynedd | Croesor STW | 109 | 2140 | Over1500 | 4.28 | 3.13 | 2.3 | 39.89 | 21.27 | 23.51 | 263044 | 344685 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6SS | LL486SS | ll48 6ss | ll486ss | Gwynedd | Gwynedd | Croesor STW | 719 | 2307 | Over1500 | 4.62 | 3.38 | 2.48 | 43 | 22.93 | 25.35 | 263605 | 344963 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL48 6SW | LL486SW | ll48 6sw | ll486sw | Gwynedd | Gwynedd | Llanfrothen STW | 1691 | 1797 | Over1500 | 3.6 | 2.63 | 1.93 | 33.49 | 17.86 | 19.74 | 261912 | 342642 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL49 9BJ | LL499BJ | ll49 9bj | ll499bj | Gwynedd | Gwynedd | Prenteg STW | 170 | 1482 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.62 | 14.73 | 16.28 | 259140 | 341252 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL49 9LY | LL499LY | ll49 9ly | ll499ly | Gwynedd | Gwynedd | Prenteg STW | 3545 | 1263 | 1200to1500 | 2.53 | 1.85 | 1.36 | 23.54 | 12.55 | 13.88 | 257190 | 338462 | Gwynedd LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Cyngor Gwynedd | Gwynedd Council
LL49 9SP | LL499SP | ll49 9sp | ll499sp | Gwynedd | Gwynedd | Prenteg STW | 656 | 1482 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.62 | 14.73 | 16.28 | 258668 | 341486 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL49 9SR | LL499SR | ll49 9sr | ll499sr | Gwynedd | Gwynedd | Prenteg STW | 1652 | 1755 | Over1500 | 3.51 | 2.57 | 1.88 | 32.71 | 17.45 | 19.28 | 258928 | 342919 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL49 9SS | LL499SS | ll49 9ss | ll499ss | Gwynedd | Gwynedd | Prenteg STW | 767 | 1482 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.62 | 14.73 | 16.28 | 258539 | 341402 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL49 9ST | LL499ST | ll49 9st | ll499st | Gwynedd | Gwynedd | Prenteg STW | 805 | 1482 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.62 | 14.73 | 16.28 | 258509 | 341459 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL49 9SU | LL499SU | ll49 9su | ll499su | Gwynedd | Gwynedd | Prenteg STW | 814 | 1631 | Over1500 | 3.26 | 2.39 | 1.75 | 30.4 | 16.21 | 17.92 | 258512 | 341514 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL49 9SW | LL499SW | ll49 9sw | ll499sw | Gwynedd | Gwynedd | Prenteg STW | 721 | 1482 | 1200to1500 | 2.97 | 2.17 | 1.59 | 27.62 | 14.73 | 16.28 | 258583 | 341381 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL49 9SY | LL499SY | ll49 9sy | ll499sy | Gwynedd | Gwynedd | Prenteg STW | 859 | 1715 | Over1500 | 3.43 | 2.51 | 1.84 | 31.96 | 17.05 | 18.84 | 258486 | 341585 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL49 9TA | LL499TA | ll49 9ta | ll499ta | Gwynedd | Gwynedd | Prenteg STW | 867 | 1715 | Over1500 | 3.43 | 2.51 | 1.84 | 31.96 | 17.05 | 18.84 | 258483 | 341599 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL49 9TB | LL499TB | ll49 9tb | ll499tb | Gwynedd | Gwynedd | Prenteg STW | 870 | 1715 | Over1500 | 3.43 | 2.51 | 1.84 | 31.96 | 17.05 | 18.84 | 258472 | 341578 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL49 9TD | LL499TD | ll49 9td | ll499td | Gwynedd | Gwynedd | Prenteg STW | 921 | 1715 | Over1500 | 3.43 | 2.51 | 1.84 | 31.96 | 17.05 | 18.84 | 258421 | 341586 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL49 9TE | LL499TE | ll49 9te | ll499te | Gwynedd | Gwynedd | Prenteg STW | 1684 | 1715 | Over1500 | 3.43 | 2.51 | 1.84 | 31.96 | 17.05 | 18.84 | 257659 | 341685 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL49 9TF | LL499TF | ll49 9tf | ll499tf | Gwynedd | Gwynedd | Prenteg STW | 2163 | 1805 | Over1500 | 3.61 | 2.64 | 1.94 | 33.64 | 17.94 | 19.83 | 257628 | 342681 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL51 9BQ | LL519BQ | ll51 9bq | ll519bq | Gwynedd | Gwynedd | Prenteg STW | 3148 | 1945 | Over1500 | 3.89 | 2.85 | 2.09 | 36.25 | 19.33 | 21.37 | 256161 | 341539 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL54 6TW | LL546TW | ll54 6tw | ll546tw | Gwynedd | Gwynedd | Rhyd Ddu STW | 1614 | 2841 | Over1500 | 5.69 | 4.16 | 3.05 | 52.95 | 28.24 | 31.21 | 257887 | 351700 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4LT | LL554LT | ll55 4lt | ll554lt | Gwynedd | Gwynedd | Beddgelert WwTW | 522 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 259111 | 348136 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4LU | LL554LU | ll55 4lu | ll554lu | Gwynedd | Gwynedd | Beddgelert WwTW | 562 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 259164 | 348167 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4LY | LL554LY | ll55 4ly | ll554ly | Gwynedd | Gwynedd | Beddgelert WwTW | 598 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 259172 | 348202 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4NA | LL554NA | ll55 4na | ll554na | Gwynedd | Gwynedd | Beddgelert WwTW | 532 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 259202 | 348127 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4NB | LL554NB | ll55 4nb | ll554nb | Gwynedd | Gwynedd | Beddgelert WwTW | 530 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 259287 | 348090 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4ND | LL554ND | ll55 4nd | ll554nd | Gwynedd | Gwynedd | Beddgelert WwTW | 625 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 259213 | 348220 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4NE | LL554NE | ll55 4ne | ll554ne | Gwynedd | Gwynedd | Beddgelert WwTW | 1376 | 2348 | Over1500 | 4.7 | 3.44 | 2.52 | 43.76 | 23.34 | 25.8 | 259991 | 348618 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4NF | LL554NF | ll55 4nf | ll554nf | Gwynedd | Gwynedd | Beddgelert WwTW | 983 | 2568 | Over1500 | 5.14 | 3.76 | 2.76 | 47.86 | 25.53 | 28.21 | 259362 | 348549 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4NG | LL554NG | ll55 4ng | ll554ng | Gwynedd | Gwynedd | Beddgelert WwTW | 1340 | 2348 | Over1500 | 4.7 | 3.44 | 2.52 | 43.76 | 23.34 | 25.8 | 259673 | 348802 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4NH | LL554NH | ll55 4nh | ll554nh | Gwynedd | Gwynedd | Toilet Block Pont Bethania Nantgwy | 154 | 2519 | Over1500 | 5.04 | 3.69 | 2.71 | 46.95 | 25.04 | 27.68 | 262517 | 350294 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4NJ | LL554NJ | ll55 4nj | ll554nj | Gwynedd | Gwynedd | Beddgelert WwTW | 700 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 259252 | 348287 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4NL | LL554NL | ll55 4nl | ll554nl | Gwynedd | Gwynedd | Toilet Block Pont Bethania Nantgwy | 745 | 2519 | Over1500 | 5.04 | 3.69 | 2.71 | 46.95 | 25.04 | 27.68 | 263200 | 349837 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4NQ | LL554NQ | ll55 4nq | ll554nq | Gwynedd | Gwynedd | Aber (Nant Gwynant) STW | 506 | 2838 | Over1500 | 5.68 | 4.16 | 3.05 | 52.9 | 28.21 | 31.18 | 262718 | 351186 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4NR | LL554NR | ll55 4nr | ll554nr | Gwynedd | Gwynedd | Toilet Block Pont Bethania Nantgwy | 450 | 2838 | Over1500 | 5.68 | 4.16 | 3.05 | 52.9 | 28.21 | 31.18 | 263080 | 350511 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4NW | LL554NW | ll55 4nw | ll554nw | Gwynedd | Gwynedd | Aber (Nant Gwynant) STW | 623 | 2656 | Over1500 | 5.32 | 3.89 | 2.85 | 49.5 | 26.4 | 29.18 | 263773 | 351407 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4UU | LL554UU | ll55 4uu | ll554uu | Gwynedd | Gwynedd | Beddgelert WwTW | 1933 | 2474 | Over1500 | 4.95 | 3.62 | 2.66 | 46.11 | 24.59 | 27.18 | 257830 | 349120 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4UY | LL554UY | ll55 4uy | ll554uy | Gwynedd | Gwynedd | Beddgelert WwTW | 708 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 258782 | 348275 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4YA | LL554YA | ll55 4ya | ll554ya | Gwynedd | Gwynedd | Beddgelert WwTW | 452 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 259048 | 348070 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4YB | LL554YB | ll55 4yb | ll554yb | Gwynedd | Gwynedd | Beddgelert WwTW | 468 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 258997 | 348083 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4YD | LL554YD | ll55 4yd | ll554yd | Gwynedd | Gwynedd | Beddgelert WwTW | 549 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 258865 | 348136 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4YE | LL554YE | ll55 4ye | ll554ye | Gwynedd | Gwynedd | Beddgelert WwTW | 475 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 258812 | 348031 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4YF | LL554YF | ll55 4yf | ll554yf | Gwynedd | Gwynedd | Nantmor STW | 443 | 2005 | Over1500 | 4.01 | 2.94 | 2.15 | 37.37 | 19.93 | 22.03 | 259322 | 345273 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4YG | LL554YG | ll55 4yg | ll554yg | Gwynedd | Gwynedd | Nantmor STW | 610 | 2015 | Over1500 | 4.03 | 2.95 | 2.16 | 37.56 | 20.03 | 22.14 | 259944 | 346122 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4YH | LL554YH | ll55 4yh | ll554yh | Gwynedd | Gwynedd | Nantmor STW | 771 | 2015 | Over1500 | 4.03 | 2.95 | 2.16 | 37.56 | 20.03 | 22.14 | 260180 | 346111 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4YJ | LL554YJ | ll55 4yj | ll554yj | Gwynedd | Gwynedd | Beddgelert WwTW | 518 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 258821 | 348084 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4YL | LL554YL | ll55 4yl | ll554yl | Gwynedd | Gwynedd | Nantmor STW | 1164 | 1913 | Over1500 | 3.83 | 2.8 | 2.05 | 35.66 | 19.02 | 21.02 | 260635 | 346110 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4YN | LL554YN | ll55 4yn | ll554yn | Gwynedd | Gwynedd | Nantmor STW | 1008 | 1747 | Over1500 | 3.5 | 2.56 | 1.88 | 32.56 | 17.37 | 19.19 | 259953 | 344708 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4YQ | LL554YQ | ll55 4yq | ll554yq | Gwynedd | Gwynedd | Beddgelert WwTW | 462 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 258896 | 348055 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
LL55 4YW | LL554YW | ll55 4yw | ll554yw | Gwynedd | Gwynedd | Beddgelert WwTW | 487 | 2505 | Over1500 | 5.01 | 3.67 | 2.69 | 46.69 | 24.9 | 27.52 | 258751 | 348005 | Snowdonia National Park LPA | NW | Coedydd Derw a Safleoedd Ystlumod Meirion / Meirionnydd Oakwoods and Bat Sites | Parc Cenedlaethol Eryri | Eryri National Park
CH1 4QL | CH14QL | ch1 4ql | ch14ql | Flintshire | Sir Y Fflint | Queensferry WwTW | 5891 | 706 | 700to900 | 1.41 | 1.03 | 0.76 | 13.15 | 7.01 | 7.75 | 337980 | 366703 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6BA | CH16BA | ch1 6ba | ch16ba | Flintshire | Sir Y Fflint | Queensferry WwTW | 3034 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 335408 | 368374 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6BB | CH16BB | ch1 6bb | ch16bb | Flintshire | Sir Y Fflint | Queensferry WwTW | 3254 | 708 | 700to900 | 1.42 | 1.04 | 0.76 | 13.18 | 7.03 | 7.77 | 335404 | 367327 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6BL | CH16BL | ch1 6bl | ch16bl | Flintshire | Sir Y Fflint | Queensferry WwTW | 3368 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 335701 | 369068 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6BP | CH16BP | ch1 6bp | ch16bp | Flintshire | Sir Y Fflint | Queensferry WwTW | 3655 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 335745 | 367101 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6BQ | CH16BQ | ch1 6bq | ch16bq | Flintshire | Sir Y Fflint | Queensferry WwTW | 2629 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 334888 | 367739 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6BR | CH16BR | ch1 6br | ch16br | Flintshire | Sir Y Fflint | Queensferry WwTW | 3021 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 335393 | 368712 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6BS | CH16BS | ch1 6bs | ch16bs | Flintshire | Sir Y Fflint | Queensferry WwTW | 4446 | 708 | 700to900 | 1.42 | 1.04 | 0.76 | 13.18 | 7.03 | 7.77 | 336739 | 367659 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6BX | CH16BX | ch1 6bx | ch16bx | Flintshire | Sir Y Fflint | Queensferry WwTW | 4015 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 336076 | 366960 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6BY | CH16BY | ch1 6by | ch16by | Flintshire | Sir Y Fflint | Queensferry WwTW | 2922 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 335300 | 368474 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6BZ | CH16BZ | ch1 6bz | ch16bz | Flintshire | Sir Y Fflint | Queensferry WwTW | 2749 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 335091 | 368076 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6DD | CH16DD | ch1 6dd | ch16dd | Flintshire | Sir Y Fflint | Queensferry WwTW | 3284 | 708 | 700to900 | 1.42 | 1.04 | 0.76 | 13.18 | 7.03 | 7.77 | 335468 | 367411 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6EB | CH16EB | ch1 6eb | ch16eb | Flintshire | Sir Y Fflint | Queensferry WwTW | 3764 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 336105 | 368001 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6HB | CH16HB | ch1 6hb | ch16hb | Flintshire | Sir Y Fflint | Queensferry WwTW | 3243 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 335559 | 369151 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6HH | CH16HH | ch1 6hh | ch16hh | Flintshire | Sir Y Fflint | Queensferry WwTW | 3306 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 335631 | 369111 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6QB | CH16QB | ch1 6qb | ch16qb | Flintshire | Sir Y Fflint | Queensferry WwTW | 5278 | 701 | 700to900 | 1.4 | 1.02 | 0.75 | 13.05 | 6.96 | 7.69 | 336951 | 365889 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6QE | CH16QE | ch1 6qe | ch16qe | Flintshire | Sir Y Fflint | Queensferry WwTW | 6012 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 337895 | 366136 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6QF | CH16QF | ch1 6qf | ch16qf | Flintshire | Sir Y Fflint | Queensferry WwTW | 5442 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 337465 | 366592 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6QG | CH16QG | ch1 6qg | ch16qg | Flintshire | Sir Y Fflint | Queensferry WwTW | 5392 | 701 | 700to900 | 1.4 | 1.02 | 0.75 | 13.05 | 6.96 | 7.69 | 337292 | 366304 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH1 6QQ | CH16QQ | ch1 6qq | ch16qq | Flintshire | Sir Y Fflint | Queensferry WwTW | 5323 | 701 | 700to900 | 1.4 | 1.02 | 0.75 | 13.05 | 6.96 | 7.69 | 337000 | 365884 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AA | CH40AA | ch4 0aa | ch40aa | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2122 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 329981 | 361860 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AB | CH40AB | ch4 0ab | ch40ab | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3550 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 331434 | 362413 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AD | CH40AD | ch4 0ad | ch40ad | Flintshire | Sir Y Fflint | Queensferry WwTW | 5143 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333604 | 363529 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AE | CH40AE | ch4 0ae | ch40ae | Flintshire | Sir Y Fflint | Queensferry WwTW | 6159 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337389 | 364944 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AF | CH40AF | ch4 0af | ch40af | Flintshire | Sir Y Fflint | Queensferry WwTW | 6166 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337408 | 364958 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AG | CH40AG | ch4 0ag | ch40ag | Flintshire | Sir Y Fflint | Queensferry WwTW | 6092 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337185 | 364781 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AH | CH40AH | ch4 0ah | ch40ah | Flintshire | Sir Y Fflint | Queensferry WwTW | 6188 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337459 | 364992 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AJ | CH40AJ | ch4 0aj | ch40aj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2170 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330030 | 361865 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AL | CH40AL | ch4 0al | ch40al | Flintshire | Sir Y Fflint | Queensferry WwTW | 5851 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337014 | 364954 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AN | CH40AN | ch4 0an | ch40an | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2035 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 329870 | 361753 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AP | CH40AP | ch4 0ap | ch40ap | Flintshire | Sir Y Fflint | Queensferry WwTW | 6244 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337404 | 364819 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AQ | CH40AQ | ch4 0aq | ch40aq | Flintshire | Sir Y Fflint | Queensferry WwTW | 5990 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337023 | 364742 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AR | CH40AR | ch4 0ar | ch40ar | Flintshire | Sir Y Fflint | Queensferry WwTW | 6237 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337395 | 364819 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AS | CH40AS | ch4 0as | ch40as | Flintshire | Sir Y Fflint | Queensferry WwTW | 6007 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337146 | 364870 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AT | CH40AT | ch4 0at | ch40at | Flintshire | Sir Y Fflint | Queensferry WwTW | 5887 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337117 | 365032 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AU | CH40AU | ch4 0au | ch40au | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2050 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 329891 | 361776 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AW | CH40AW | ch4 0aw | ch40aw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2117 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 329909 | 361585 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AX | CH40AX | ch4 0ax | ch40ax | Flintshire | Sir Y Fflint | Queensferry WwTW | 6002 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337076 | 364789 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AY | CH40AY | ch4 0ay | ch40ay | Flintshire | Sir Y Fflint | Queensferry WwTW | 5943 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337089 | 364901 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0AZ | CH40AZ | ch4 0az | ch40az | Flintshire | Sir Y Fflint | Queensferry WwTW | 5816 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337033 | 365038 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BB | CH40BB | ch4 0bb | ch40bb | Flintshire | Sir Y Fflint | Queensferry WwTW | 3652 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 334993 | 365973 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BE | CH40BE | ch4 0be | ch40be | Flintshire | Sir Y Fflint | Queensferry WwTW | 5783 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 336981 | 365023 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BG | CH40BG | ch4 0bg | ch40bg | Flintshire | Sir Y Fflint | Queensferry WwTW | 5914 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337011 | 364849 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BH | CH40BH | ch4 0bh | ch40bh | Flintshire | Sir Y Fflint | Queensferry WwTW | 5375 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 336785 | 365447 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BJ | CH40BJ | ch4 0bj | ch40bj | Flintshire | Sir Y Fflint | Queensferry WwTW | 5444 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 336815 | 365370 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BL | CH40BL | ch4 0bl | ch40bl | Flintshire | Sir Y Fflint | Queensferry WwTW | 5375 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 336683 | 365306 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BN | CH40BN | ch4 0bn | ch40bn | Flintshire | Sir Y Fflint | Queensferry WwTW | 5789 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 336921 | 364936 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BP | CH40BP | ch4 0bp | ch40bp | Flintshire | Sir Y Fflint | Queensferry WwTW | 5503 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 336823 | 365279 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BQ | CH40BQ | ch4 0bq | ch40bq | Flintshire | Sir Y Fflint | Queensferry WwTW | 5910 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 336913 | 364735 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BR | CH40BR | ch4 0br | ch40br | Flintshire | Sir Y Fflint | Queensferry WwTW | 5373 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 336693 | 365323 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BS | CH40BS | ch4 0bs | ch40bs | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2092 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 329887 | 361600 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BT | CH40BT | ch4 0bt | ch40bt | Flintshire | Sir Y Fflint | Queensferry WwTW | 4317 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 336031 | 366223 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BU | CH40BU | ch4 0bu | ch40bu | Flintshire | Sir Y Fflint | Queensferry WwTW | 4997 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334622 | 364059 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BW | CH40BW | ch4 0bw | ch40bw | Flintshire | Sir Y Fflint | Queensferry WwTW | 4349 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 336029 | 366161 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BX | CH40BX | ch4 0bx | ch40bx | Flintshire | Sir Y Fflint | Queensferry WwTW | 5897 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 336941 | 364788 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BY | CH40BY | ch4 0by | ch40by | Flintshire | Sir Y Fflint | Queensferry WwTW | 5276 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 335891 | 364587 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0BZ | CH40BZ | ch4 0bz | ch40bz | Flintshire | Sir Y Fflint | Queensferry WwTW | 4502 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 335507 | 365286 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DA | CH40DA | ch4 0da | ch40da | Flintshire | Sir Y Fflint | Lavister WwTW | 5160 | 707 | 700to900 | 1.41 | 1.03 | 0.76 | 13.16 | 7.02 | 7.76 | 335282 | 363067 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DB | CH40DB | ch4 0db | ch40db | Flintshire | Sir Y Fflint | Lavister WwTW | 5791 | 701 | 700to900 | 1.4 | 1.02 | 0.75 | 13.05 | 6.96 | 7.69 | 336739 | 364225 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DD | CH40DD | ch4 0dd | ch40dd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2092 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 329899 | 361640 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DE | CH40DE | ch4 0de | ch40de | Flintshire | Sir Y Fflint | Queensferry WwTW | 5396 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334999 | 363807 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DF | CH40DF | ch4 0df | ch40df | Flintshire | Sir Y Fflint | Queensferry WwTW | 5764 | 701 | 700to900 | 1.4 | 1.02 | 0.75 | 13.05 | 6.96 | 7.69 | 336215 | 364223 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DH | CH40DH | ch4 0dh | ch40dh | Flintshire | Sir Y Fflint | Queensferry WwTW | 5245 | 701 | 700to900 | 1.4 | 1.02 | 0.75 | 13.05 | 6.96 | 7.69 | 335697 | 364462 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DL | CH40DL | ch4 0dl | ch40dl | Flintshire | Sir Y Fflint | Queensferry WwTW | 4862 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334202 | 364017 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DN | CH40DN | ch4 0dn | ch40dn | Flintshire | Sir Y Fflint | Queensferry WwTW | 5573 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 335191 | 363713 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DP | CH40DP | ch4 0dp | ch40dp | Flintshire | Sir Y Fflint | Queensferry WwTW | 5416 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 335053 | 363814 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DQ | CH40DQ | ch4 0dq | ch40dq | Flintshire | Sir Y Fflint | Queensferry WwTW | 5025 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 335014 | 364245 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DR | CH40DR | ch4 0dr | ch40dr | Flintshire | Sir Y Fflint | Queensferry WwTW | 4754 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334613 | 364327 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DS | CH40DS | ch4 0ds | ch40ds | Flintshire | Sir Y Fflint | Queensferry WwTW | 5275 | 701 | 700to900 | 1.4 | 1.02 | 0.75 | 13.05 | 6.96 | 7.69 | 335762 | 364477 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DT | CH40DT | ch4 0dt | ch40dt | Flintshire | Sir Y Fflint | Queensferry WwTW | 4969 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334681 | 364120 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DU | CH40DU | ch4 0du | ch40du | Flintshire | Sir Y Fflint | Queensferry WwTW | 5373 | 701 | 700to900 | 1.4 | 1.02 | 0.75 | 13.05 | 6.96 | 7.69 | 335603 | 364226 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DW | CH40DW | ch4 0dw | ch40dw | Flintshire | Sir Y Fflint | Queensferry WwTW | 5558 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 335378 | 363845 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DX | CH40DX | ch4 0dx | ch40dx | Flintshire | Sir Y Fflint | Queensferry WwTW | 5519 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 335481 | 363960 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DY | CH40DY | ch4 0dy | ch40dy | Flintshire | Sir Y Fflint | Queensferry WwTW | 5376 | 701 | 700to900 | 1.4 | 1.02 | 0.75 | 13.05 | 6.96 | 7.69 | 335599 | 364219 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0DZ | CH40DZ | ch4 0dz | ch40dz | Flintshire | Sir Y Fflint | Queensferry WwTW | 5553 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 335469 | 363910 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EB | CH40EB | ch4 0eb | ch40eb | Flintshire | Sir Y Fflint | Hope WwTW | 2835 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330438 | 360923 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0ED | CH40ED | ch4 0ed | ch40ed | Flintshire | Sir Y Fflint | Queensferry WwTW | 5206 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 332991 | 363354 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EE | CH40EE | ch4 0ee | ch40ee | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 4613 | 773 | 700to900 | 1.55 | 1.13 | 0.83 | 14.41 | 7.68 | 8.49 | 332336 | 363444 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EF | CH40EF | ch4 0ef | ch40ef | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 4204 | 773 | 700to900 | 1.55 | 1.13 | 0.83 | 14.41 | 7.68 | 8.49 | 331896 | 363491 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EG | CH40EG | ch4 0eg | ch40eg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 4460 | 773 | 700to900 | 1.55 | 1.13 | 0.83 | 14.41 | 7.68 | 8.49 | 332174 | 363456 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EH | CH40EH | ch4 0eh | ch40eh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 4518 | 773 | 700to900 | 1.55 | 1.13 | 0.83 | 14.41 | 7.68 | 8.49 | 332362 | 362852 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EL | CH40EL | ch4 0el | ch40el | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2134 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 329925 | 362859 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EN | CH40EN | ch4 0en | ch40en | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2544 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 330351 | 362861 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EP | CH40EP | ch4 0ep | ch40ep | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1969 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 329806 | 362670 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EQ | CH40EQ | ch4 0eq | ch40eq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 4375 | 767 | 700to900 | 1.54 | 1.12 | 0.82 | 14.3 | 7.62 | 8.43 | 331982 | 363765 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0ER | CH40ER | ch4 0er | ch40er | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2987 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 330713 | 363194 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0ES | CH40ES | ch4 0es | ch40es | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3145 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 331022 | 362498 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0ET | CH40ET | ch4 0et | ch40et | Flintshire | Sir Y Fflint | Hope WwTW | 2460 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330302 | 360537 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EU | CH40EU | ch4 0eu | ch40eu | Flintshire | Sir Y Fflint | Hope WwTW | 2315 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 331116 | 360339 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EW | CH40EW | ch4 0ew | ch40ew | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 4530 | 773 | 700to900 | 1.55 | 1.13 | 0.83 | 14.41 | 7.68 | 8.49 | 332339 | 363063 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EX | CH40EX | ch4 0ex | ch40ex | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3170 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 331017 | 361708 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EY | CH40EY | ch4 0ey | ch40ey | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2494 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330258 | 361439 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0EZ | CH40EZ | ch4 0ez | ch40ez | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2531 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330221 | 361235 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FA | CH40FA | ch4 0fa | ch40fa | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 5314 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333124 | 363127 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FB | CH40FB | ch4 0fb | ch40fb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 5155 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 332956 | 363163 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FD | CH40FD | ch4 0fd | ch40fd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 5220 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333007 | 363243 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FE | CH40FE | ch4 0fe | ch40fe | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 5440 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333255 | 363112 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FF | CH40FF | ch4 0ff | ch40ff | Flintshire | Sir Y Fflint | Queensferry WwTW | 5497 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333316 | 363107 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FG | CH40FG | ch4 0fg | ch40fg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 5514 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333339 | 363053 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FH | CH40FH | ch4 0fh | ch40fh | Flintshire | Sir Y Fflint | Queensferry WwTW | 5497 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333370 | 363117 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FL | CH40FL | ch4 0fl | ch40fl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2041 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 329846 | 361638 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FN | CH40FN | ch4 0fn | ch40fn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2071 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 329888 | 361679 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FP | CH40FP | ch4 0fp | ch40fp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2197 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330004 | 361625 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FQ | CH40FQ | ch4 0fq | ch40fq | Flintshire | Sir Y Fflint | Queensferry WwTW | 5656 | 707 | 700to900 | 1.41 | 1.03 | 0.76 | 13.16 | 7.02 | 7.76 | 334667 | 363352 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FR | CH40FR | ch4 0fr | ch40fr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2171 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330001 | 361715 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FS | CH40FS | ch4 0fs | ch40fs | Flintshire | Sir Y Fflint | Queensferry WwTW | 5562 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334466 | 363368 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FT | CH40FT | ch4 0ft | ch40ft | Flintshire | Sir Y Fflint | Queensferry WwTW | 5632 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334473 | 363296 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FW | CH40FW | ch4 0fw | ch40fw | Flintshire | Sir Y Fflint | Queensferry WwTW | 5662 | 707 | 700to900 | 1.41 | 1.03 | 0.76 | 13.16 | 7.02 | 7.76 | 334613 | 363322 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FX | CH40FX | ch4 0fx | ch40fx | Flintshire | Sir Y Fflint | Queensferry WwTW | 5083 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334706 | 364005 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FY | CH40FY | ch4 0fy | ch40fy | Flintshire | Sir Y Fflint | Lavister WwTW | 5676 | 707 | 700to900 | 1.41 | 1.03 | 0.76 | 13.16 | 7.02 | 7.76 | 334722 | 363339 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0FZ | CH40FZ | ch4 0fz | ch40fz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2317 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330206 | 362203 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GA | CH40GA | ch4 0ga | ch40ga | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2535 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330322 | 361509 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GB | CH40GB | ch4 0gb | ch40gb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2232 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330061 | 361703 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GD | CH40GD | ch4 0gd | ch40gd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2213 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330066 | 361820 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GE | CH40GE | ch4 0ge | ch40ge | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2184 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330023 | 361753 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GF | CH40GF | ch4 0gf | ch40gf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2277 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330107 | 361706 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GG | CH40GG | ch4 0gg | ch40gg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2315 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330151 | 361728 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GH | CH40GH | ch4 0gh | ch40gh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2282 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330132 | 361798 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GJ | CH40GJ | ch4 0gj | ch40gj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2785 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 330640 | 362652 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GL | CH40GL | ch4 0gl | ch40gl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2873 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 330732 | 362637 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GN | CH40GN | ch4 0gn | ch40gn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2889 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 330755 | 362584 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GP | CH40GP | ch4 0gp | ch40gp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2734 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 330599 | 362581 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GQ | CH40GQ | ch4 0gq | ch40gq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2730 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 330578 | 362690 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GS | CH40GS | ch4 0gs | ch40gs | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2066 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 329743 | 361307 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GX | CH40GX | ch4 0gx | ch40gx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2344 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330225 | 362027 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GY | CH40GY | ch4 0gy | ch40gy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2420 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330011 | 361057 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0GZ | CH40GZ | ch4 0gz | ch40gz | Flintshire | Sir Y Fflint | Queensferry WwTW | 3664 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 334966 | 365929 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HA | CH40HA | ch4 0ha | ch40ha | Flintshire | Sir Y Fflint | Queensferry WwTW | 4755 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334613 | 364326 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HB | CH40HB | ch4 0hb | ch40hb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2981 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 330751 | 361385 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HD | CH40HD | ch4 0hd | ch40hd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2394 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330107 | 361318 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HE | CH40HE | ch4 0he | ch40he | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2424 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330127 | 361289 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HF | CH40HF | ch4 0hf | ch40hf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2331 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330021 | 361277 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HG | CH40HG | ch4 0hg | ch40hg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 5007 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 332846 | 362921 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HH | CH40HH | ch4 0hh | ch40hh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2420 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330167 | 361404 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HJ | CH40HJ | ch4 0hj | ch40hj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2533 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330204 | 361193 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HL | CH40HL | ch4 0hl | ch40hl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2320 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330097 | 361508 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HN | CH40HN | ch4 0hn | ch40hn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2545 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330142 | 361036 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HP | CH40HP | ch4 0hp | ch40hp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2606 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330148 | 360920 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HQ | CH40HQ | ch4 0hq | ch40hq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2542 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330290 | 361386 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HR | CH40HR | ch4 0hr | ch40hr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2688 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330156 | 360775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HS | CH40HS | ch4 0hs | ch40hs | Flintshire | Sir Y Fflint | Hope WwTW | 2674 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330227 | 360744 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HT | CH40HT | ch4 0ht | ch40ht | Flintshire | Sir Y Fflint | Hope WwTW | 2572 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330308 | 360650 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HU | CH40HU | ch4 0hu | ch40hu | Flintshire | Sir Y Fflint | Hope WwTW | 2027 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 330498 | 360117 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HW | CH40HW | ch4 0hw | ch40hw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2427 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330041 | 361098 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HX | CH40HX | ch4 0hx | ch40hx | Flintshire | Sir Y Fflint | Hope WwTW | 2428 | 811 | 700to900 | 1.62 | 1.19 | 0.87 | 15.12 | 8.06 | 8.91 | 330620 | 360519 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HY | CH40HY | ch4 0hy | ch40hy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2266 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 329929 | 361234 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0HZ | CH40HZ | ch4 0hz | ch40hz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2285 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 329964 | 361263 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JA | CH40JA | ch4 0ja | ch40ja | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2289 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330076 | 361545 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JB | CH40JB | ch4 0jb | ch40jb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2226 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 329988 | 361478 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JD | CH40JD | ch4 0jd | ch40jd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2347 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330201 | 361814 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JE | CH40JE | ch4 0je | ch40je | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2389 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330270 | 362026 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JF | CH40JF | ch4 0jf | ch40jf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2492 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330321 | 361674 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JG | CH40JG | ch4 0jg | ch40jg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2377 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 329970 | 361072 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JH | CH40JH | ch4 0jh | ch40jh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2415 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330303 | 362289 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JJ | CH40JJ | ch4 0jj | ch40jj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2493 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330382 | 362227 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JL | CH40JL | ch4 0jl | ch40jl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2439 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330322 | 362052 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JN | CH40JN | ch4 0jn | ch40jn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2180 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330044 | 361889 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JP | CH40JP | ch4 0jp | ch40jp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2757 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330638 | 362015 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JQ | CH40JQ | ch4 0jq | ch40jq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2443 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330331 | 362143 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JR | CH40JR | ch4 0jr | ch40jr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2095 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 329779 | 361315 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JS | CH40JS | ch4 0js | ch40js | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2252 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330021 | 361493 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JT | CH40JT | ch4 0jt | ch40jt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2090 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 329796 | 361364 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JU | CH40JU | ch4 0ju | ch40ju | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2112 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 329846 | 361425 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JW | CH40JW | ch4 0jw | ch40jw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2338 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 330092 | 361436 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JX | CH40JX | ch4 0jx | ch40jx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2277 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 329893 | 361138 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JY | CH40JY | ch4 0jy | ch40jy | Flintshire | Sir Y Fflint | Hope WwTW | 2194 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 329797 | 360147 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0JZ | CH40JZ | ch4 0jz | ch40jz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2482 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330339 | 361821 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LB | CH40LB | ch4 0lb | ch40lb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2713 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330595 | 362411 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LD | CH40LD | ch4 0ld | ch40ld | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2429 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330279 | 361787 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LE | CH40LE | ch4 0le | ch40le | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2458 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330329 | 361920 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LF | CH40LF | ch4 0lf | ch40lf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2506 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330394 | 362145 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LG | CH40LG | ch4 0lg | ch40lg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2623 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 330488 | 362576 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LH | CH40LH | ch4 0lh | ch40lh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2408 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330261 | 361802 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LJ | CH40LJ | ch4 0lj | ch40lj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2650 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 330515 | 362576 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LL | CH40LL | ch4 0ll | ch40ll | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2834 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330722 | 362284 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LN | CH40LN | ch4 0ln | ch40ln | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2887 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330776 | 362170 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LP | CH40LP | ch4 0lp | ch40lp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2700 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330589 | 362209 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LQ | CH40LQ | ch4 0lq | ch40lq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2559 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330448 | 362202 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LR | CH40LR | ch4 0lr | ch40lr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2814 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330701 | 362109 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LS | CH40LS | ch4 0ls | ch40ls | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2459 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330322 | 361864 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LT | CH40LT | ch4 0lt | ch40lt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2582 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330467 | 362067 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LU | CH40LU | ch4 0lu | ch40lu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2782 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330671 | 362171 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LW | CH40LW | ch4 0lw | ch40lw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2788 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330677 | 362218 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LX | CH40LX | ch4 0lx | ch40lx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2868 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330757 | 362213 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LY | CH40LY | ch4 0ly | ch40ly | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2508 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330394 | 362348 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0LZ | CH40LZ | ch4 0lz | ch40lz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2474 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330359 | 362359 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NA | CH40NA | ch4 0na | ch40na | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2484 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 330350 | 362555 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NB | CH40NB | ch4 0nb | ch40nb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2602 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 330489 | 362121 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0ND | CH40ND | ch4 0nd | ch40nd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2733 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330621 | 362144 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NE | CH40NE | ch4 0ne | ch40ne | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2658 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330545 | 362116 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NF | CH40NF | ch4 0nf | ch40nf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2697 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330579 | 362022 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NG | CH40NG | ch4 0ng | ch40ng | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2766 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330655 | 362267 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NH | CH40NH | ch4 0nh | ch40nh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2627 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330516 | 362251 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NJ | CH40NJ | ch4 0nj | ch40nj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2683 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330572 | 362190 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NN | CH40NN | ch4 0nn | ch40nn | Flintshire | Sir Y Fflint | Queensferry WwTW | 5101 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333539 | 363556 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NP | CH40NP | ch4 0np | ch40np | Flintshire | Sir Y Fflint | Queensferry WwTW | 5010 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333949 | 363766 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NQ | CH40NQ | ch4 0nq | ch40nq | Flintshire | Sir Y Fflint | Queensferry WwTW | 4809 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334237 | 364088 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NR | CH40NR | ch4 0nr | ch40nr | Flintshire | Sir Y Fflint | Queensferry WwTW | 5109 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333680 | 363583 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NS | CH40NS | ch4 0ns | ch40ns | Flintshire | Sir Y Fflint | Queensferry WwTW | 5013 | 741 | 700to900 | 1.48 | 1.09 | 0.8 | 13.81 | 7.37 | 8.14 | 333479 | 363633 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NT | CH40NT | ch4 0nt | ch40nt | Flintshire | Sir Y Fflint | Queensferry WwTW | 5259 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333407 | 363366 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NU | CH40NU | ch4 0nu | ch40nu | Flintshire | Sir Y Fflint | Queensferry WwTW | 5454 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333371 | 363161 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NW | CH40NW | ch4 0nw | ch40nw | Flintshire | Sir Y Fflint | Queensferry WwTW | 4916 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334153 | 363939 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NX | CH40NX | ch4 0nx | ch40nx | Flintshire | Sir Y Fflint | Queensferry WwTW | 5067 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333868 | 363681 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NY | CH40NY | ch4 0ny | ch40ny | Flintshire | Sir Y Fflint | Queensferry WwTW | 5262 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333747 | 363443 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0NZ | CH40NZ | ch4 0nz | ch40nz | Flintshire | Sir Y Fflint | Queensferry WwTW | 5104 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333902 | 363652 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PA | CH40PA | ch4 0pa | ch40pa | Flintshire | Sir Y Fflint | Queensferry WwTW | 5605 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333831 | 363110 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PB | CH40PB | ch4 0pb | ch40pb | Flintshire | Sir Y Fflint | Queensferry WwTW | 5322 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333407 | 363302 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PD | CH40PD | ch4 0pd | ch40pd | Flintshire | Sir Y Fflint | Queensferry WwTW | 5201 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333886 | 363546 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PE | CH40PE | ch4 0pe | ch40pe | Flintshire | Sir Y Fflint | Queensferry WwTW | 5174 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333687 | 363518 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PF | CH40PF | ch4 0pf | ch40pf | Flintshire | Sir Y Fflint | Queensferry WwTW | 5211 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333703 | 363484 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PG | CH40PG | ch4 0pg | ch40pg | Flintshire | Sir Y Fflint | Queensferry WwTW | 5168 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333205 | 363422 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PH | CH40PH | ch4 0ph | ch40ph | Flintshire | Sir Y Fflint | Queensferry WwTW | 5200 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333788 | 363518 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PJ | CH40PJ | ch4 0pj | ch40pj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2676 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330562 | 362354 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PL | CH40PL | ch4 0pl | ch40pl | Flintshire | Sir Y Fflint | Queensferry WwTW | 5403 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333440 | 363226 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PN | CH40PN | ch4 0pn | ch40pn | Flintshire | Sir Y Fflint | Queensferry WwTW | 5385 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333342 | 363226 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PP | CH40PP | ch4 0pp | ch40pp | Flintshire | Sir Y Fflint | Queensferry WwTW | 5366 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333252 | 363229 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PQ | CH40PQ | ch4 0pq | ch40pq | Flintshire | Sir Y Fflint | Queensferry WwTW | 5257 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333161 | 363325 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PR | CH40PR | ch4 0pr | ch40pr | Flintshire | Sir Y Fflint | Queensferry WwTW | 5633 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334062 | 363148 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PS | CH40PS | ch4 0ps | ch40ps | Flintshire | Sir Y Fflint | Queensferry WwTW | 5547 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333990 | 363216 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PT | CH40PT | ch4 0pt | ch40pt | Flintshire | Sir Y Fflint | Queensferry WwTW | 5307 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333118 | 363269 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PU | CH40PU | ch4 0pu | ch40pu | Flintshire | Sir Y Fflint | Queensferry WwTW | 5330 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333138 | 363248 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PW | CH40PW | ch4 0pw | ch40pw | Flintshire | Sir Y Fflint | Queensferry WwTW | 5369 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333309 | 363236 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PX | CH40PX | ch4 0px | ch40px | Flintshire | Sir Y Fflint | Queensferry WwTW | 5365 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 333167 | 363217 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PY | CH40PY | ch4 0py | ch40py | Flintshire | Sir Y Fflint | Queensferry WwTW | 5519 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333901 | 363219 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0PZ | CH40PZ | ch4 0pz | ch40pz | Flintshire | Sir Y Fflint | Queensferry WwTW | 5632 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333940 | 363113 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QA | CH40QA | ch4 0qa | ch40qa | Flintshire | Sir Y Fflint | Queensferry WwTW | 5533 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334201 | 363300 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QB | CH40QB | ch4 0qb | ch40qb | Flintshire | Sir Y Fflint | Queensferry WwTW | 5008 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334400 | 363942 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QD | CH40QD | ch4 0qd | ch40qd | Flintshire | Sir Y Fflint | Queensferry WwTW | 5108 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334556 | 363903 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QE | CH40QE | ch4 0qe | ch40qe | Flintshire | Sir Y Fflint | Queensferry WwTW | 5027 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334507 | 363970 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QF | CH40QF | ch4 0qf | ch40qf | Flintshire | Sir Y Fflint | Queensferry WwTW | 5157 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334646 | 363892 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QG | CH40QG | ch4 0qg | ch40qg | Flintshire | Sir Y Fflint | Queensferry WwTW | 4974 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334427 | 363991 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QH | CH40QH | ch4 0qh | ch40qh | Flintshire | Sir Y Fflint | Queensferry WwTW | 5153 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334585 | 363867 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QJ | CH40QJ | ch4 0qj | ch40qj | Flintshire | Sir Y Fflint | Queensferry WwTW | 5584 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333955 | 363167 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QL | CH40QL | ch4 0ql | ch40ql | Flintshire | Sir Y Fflint | Queensferry WwTW | 5485 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334077 | 363308 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QN | CH40QN | ch4 0qn | ch40qn | Flintshire | Sir Y Fflint | Queensferry WwTW | 5163 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334267 | 363718 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QP | CH40QP | ch4 0qp | ch40qp | Flintshire | Sir Y Fflint | Queensferry WwTW | 5312 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333966 | 363454 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QQ | CH40QQ | ch4 0qq | ch40qq | Flintshire | Sir Y Fflint | Queensferry WwTW | 5141 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334203 | 363717 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QR | CH40QR | ch4 0qr | ch40qr | Flintshire | Sir Y Fflint | Queensferry WwTW | 5328 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333664 | 363353 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QS | CH40QS | ch4 0qs | ch40qs | Flintshire | Sir Y Fflint | Queensferry WwTW | 5366 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333658 | 363313 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QT | CH40QT | ch4 0qt | ch40qt | Flintshire | Sir Y Fflint | Queensferry WwTW | 5378 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334070 | 363419 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QU | CH40QU | ch4 0qu | ch40qu | Flintshire | Sir Y Fflint | Queensferry WwTW | 5360 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333996 | 363414 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QW | CH40QW | ch4 0qw | ch40qw | Flintshire | Sir Y Fflint | Queensferry WwTW | 5370 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333862 | 363363 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QX | CH40QX | ch4 0qx | ch40qx | Flintshire | Sir Y Fflint | Queensferry WwTW | 5421 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334031 | 363361 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QY | CH40QY | ch4 0qy | ch40qy | Flintshire | Sir Y Fflint | Queensferry WwTW | 5390 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334105 | 363418 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0QZ | CH40QZ | ch4 0qz | ch40qz | Flintshire | Sir Y Fflint | Queensferry WwTW | 4937 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334407 | 364023 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RA | CH40RA | ch4 0ra | ch40ra | Flintshire | Sir Y Fflint | Queensferry WwTW | 5469 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333808 | 363245 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RB | CH40RB | ch4 0rb | ch40rb | Flintshire | Sir Y Fflint | Queensferry WwTW | 5442 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333632 | 363228 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RD | CH40RD | ch4 0rd | ch40rd | Flintshire | Sir Y Fflint | Queensferry WwTW | 5417 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333557 | 363237 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RE | CH40RE | ch4 0re | ch40re | Flintshire | Sir Y Fflint | Queensferry WwTW | 5030 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334191 | 363832 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RF | CH40RF | ch4 0rf | ch40rf | Flintshire | Sir Y Fflint | Queensferry WwTW | 4995 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334227 | 363883 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RG | CH40RG | ch4 0rg | ch40rg | Flintshire | Sir Y Fflint | Queensferry WwTW | 5175 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333989 | 363606 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RH | CH40RH | ch4 0rh | ch40rh | Flintshire | Sir Y Fflint | Queensferry WwTW | 5488 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333914 | 363255 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RJ | CH40RJ | ch4 0rj | ch40rj | Flintshire | Sir Y Fflint | Queensferry WwTW | 5459 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333683 | 363223 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RL | CH40RL | ch4 0rl | ch40rl | Flintshire | Sir Y Fflint | Queensferry WwTW | 5062 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334002 | 363729 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RN | CH40RN | ch4 0rn | ch40rn | Flintshire | Sir Y Fflint | Queensferry WwTW | 5272 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333853 | 363462 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RP | CH40RP | ch4 0rp | ch40rp | Flintshire | Sir Y Fflint | Queensferry WwTW | 5174 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333903 | 363579 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RQ | CH40RQ | ch4 0rq | ch40rq | Flintshire | Sir Y Fflint | Queensferry WwTW | 5152 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334050 | 363650 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RR | CH40RR | ch4 0rr | ch40rr | Flintshire | Sir Y Fflint | Queensferry WwTW | 5304 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333915 | 363447 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RS | CH40RS | ch4 0rs | ch40rs | Flintshire | Sir Y Fflint | Queensferry WwTW | 5460 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334021 | 363317 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RT | CH40RT | ch4 0rt | ch40rt | Flintshire | Sir Y Fflint | Queensferry WwTW | 5470 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333778 | 363236 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RU | CH40RU | ch4 0ru | ch40ru | Flintshire | Sir Y Fflint | Lavister WwTW | 5716 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334094 | 362939 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RW | CH40RW | ch4 0rw | ch40rw | Flintshire | Sir Y Fflint | Queensferry WwTW | 5254 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333976 | 363519 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RX | CH40RX | ch4 0rx | ch40rx | Flintshire | Sir Y Fflint | Queensferry WwTW | 5405 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333884 | 363333 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RY | CH40RY | ch4 0ry | ch40ry | Flintshire | Sir Y Fflint | Queensferry WwTW | 5433 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333654 | 363243 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0RZ | CH40RZ | ch4 0rz | ch40rz | Flintshire | Sir Y Fflint | Queensferry WwTW | 5385 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333629 | 363286 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SA | CH40SA | ch4 0sa | ch40sa | Flintshire | Sir Y Fflint | Queensferry WwTW | 5578 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334193 | 363249 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SB | CH40SB | ch4 0sb | ch40sb | Flintshire | Sir Y Fflint | Queensferry WwTW | 5505 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333675 | 363174 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SD | CH40SD | ch4 0sd | ch40sd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 4512 | 773 | 700to900 | 1.55 | 1.13 | 0.83 | 14.41 | 7.68 | 8.49 | 332349 | 362899 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SE | CH40SE | ch4 0se | ch40se | Flintshire | Sir Y Fflint | Queensferry WwTW | 5385 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334375 | 363523 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SF | CH40SF | ch4 0sf | ch40sf | Flintshire | Sir Y Fflint | Queensferry WwTW | 5343 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334357 | 363561 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SG | CH40SG | ch4 0sg | ch40sg | Flintshire | Sir Y Fflint | Queensferry WwTW | 5216 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334388 | 363710 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SH | CH40SH | ch4 0sh | ch40sh | Flintshire | Sir Y Fflint | Queensferry WwTW | 5288 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334492 | 363677 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SJ | CH40SJ | ch4 0sj | ch40sj | Flintshire | Sir Y Fflint | Queensferry WwTW | 5560 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334313 | 363311 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SL | CH40SL | ch4 0sl | ch40sl | Flintshire | Sir Y Fflint | Queensferry WwTW | 5606 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334303 | 363259 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SN | CH40SN | ch4 0sn | ch40sn | Flintshire | Sir Y Fflint | Queensferry WwTW | 5449 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334466 | 363490 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SP | CH40SP | ch4 0sp | ch40sp | Flintshire | Sir Y Fflint | Queensferry WwTW | 5371 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334416 | 363554 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SQ | CH40SQ | ch4 0sq | ch40sq | Flintshire | Sir Y Fflint | Queensferry WwTW | 5322 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334506 | 363646 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SR | CH40SR | ch4 0sr | ch40sr | Flintshire | Sir Y Fflint | Queensferry WwTW | 5443 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334396 | 363469 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SS | CH40SS | ch4 0ss | ch40ss | Flintshire | Sir Y Fflint | Queensferry WwTW | 5404 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334285 | 363467 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0ST | CH40ST | ch4 0st | ch40st | Flintshire | Sir Y Fflint | Queensferry WwTW | 5280 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334304 | 363607 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SU | CH40SU | ch4 0su | ch40su | Flintshire | Sir Y Fflint | Queensferry WwTW | 5344 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334255 | 363520 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SW | CH40SW | ch4 0sw | ch40sw | Flintshire | Sir Y Fflint | Queensferry WwTW | 5439 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334427 | 363485 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SX | CH40SX | ch4 0sx | ch40sx | Flintshire | Sir Y Fflint | Queensferry WwTW | 5309 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334301 | 363575 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SY | CH40SY | ch4 0sy | ch40sy | Flintshire | Sir Y Fflint | Queensferry WwTW | 5339 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 334194 | 363503 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0SZ | CH40SZ | ch4 0sz | ch40sz | Flintshire | Sir Y Fflint | Queensferry WwTW | 5332 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334163 | 363499 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TA | CH40TA | ch4 0ta | ch40ta | Flintshire | Sir Y Fflint | Queensferry WwTW | 5571 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334398 | 363332 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TB | CH40TB | ch4 0tb | ch40tb | Flintshire | Sir Y Fflint | Queensferry WwTW | 5506 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334341 | 363379 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TD | CH40TD | ch4 0td | ch40td | Flintshire | Sir Y Fflint | Queensferry WwTW | 5617 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333610 | 363044 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TE | CH40TE | ch4 0te | ch40te | Flintshire | Sir Y Fflint | Queensferry WwTW | 5618 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 334230 | 363220 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TF | CH40TF | ch4 0tf | ch40tf | Flintshire | Sir Y Fflint | Queensferry WwTW | 5578 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333610 | 363084 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TG | CH40TG | ch4 0tg | ch40tg | Flintshire | Sir Y Fflint | Queensferry WwTW | 5607 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333767 | 363092 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TH | CH40TH | ch4 0th | ch40th | Flintshire | Sir Y Fflint | Queensferry WwTW | 4975 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334553 | 364049 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TJ | CH40TJ | ch4 0tj | ch40tj | Flintshire | Sir Y Fflint | Queensferry WwTW | 4932 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334519 | 364080 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TL | CH40TL | ch4 0tl | ch40tl | Flintshire | Sir Y Fflint | Queensferry WwTW | 5429 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334673 | 363604 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TN | CH40TN | ch4 0tn | ch40tn | Flintshire | Sir Y Fflint | Queensferry WwTW | 5522 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334681 | 363505 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TP | CH40TP | ch4 0tp | ch40tp | Flintshire | Sir Y Fflint | Queensferry WwTW | 5499 | 707 | 700to900 | 1.41 | 1.03 | 0.76 | 13.16 | 7.02 | 7.76 | 334573 | 363482 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TQ | CH40TQ | ch4 0tq | ch40tq | Flintshire | Sir Y Fflint | Queensferry WwTW | 5620 | 707 | 700to900 | 1.41 | 1.03 | 0.76 | 13.16 | 7.02 | 7.76 | 334752 | 363430 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TR | CH40TR | ch4 0tr | ch40tr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2802 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330690 | 362283 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TS | CH40TS | ch4 0ts | ch40ts | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2905 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330793 | 362293 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TT | CH40TT | ch4 0tt | ch40tt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2816 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330704 | 362312 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TU | CH40TU | ch4 0tu | ch40tu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2833 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330719 | 362355 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0TW | CH40TW | ch4 0tw | ch40tw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2929 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330809 | 362452 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0XA | CH40XA | ch4 0xa | ch40xa | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2602 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 330455 | 362651 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0XB | CH40XB | ch4 0xb | ch40xb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2604 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 330443 | 362729 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0XD | CH40XD | ch4 0xd | ch40xd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2540 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 330403 | 362582 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0YR | CH40YR | ch4 0yr | ch40yr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2648 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330527 | 362446 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0YS | CH40YS | ch4 0ys | ch40ys | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2678 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 330551 | 362517 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0YT | CH40YT | ch4 0yt | ch40yt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2841 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 330716 | 362502 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0YU | CH40YU | ch4 0yu | ch40yu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2816 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330696 | 362440 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0YX | CH40YX | ch4 0yx | ch40yx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2794 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330679 | 362374 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 0YY | CH40YY | ch4 0yy | ch40yy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2782 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 330669 | 362338 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8BF | CH48BF | ch4 8bf | ch48bf | Flintshire | Sir Y Fflint | Lavister WwTW | 6534 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338038 | 365043 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8BT | CH48BT | ch4 8bt | ch48bt | Flintshire | Sir Y Fflint | Lavister WwTW | 6508 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338471 | 364981 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8FA | CH48FA | ch4 8fa | ch48fa | Flintshire | Sir Y Fflint | Queensferry WwTW | 6247 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337497 | 364944 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8FB | CH48FB | ch4 8fb | ch48fb | Flintshire | Sir Y Fflint | Queensferry WwTW | 6225 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337520 | 365015 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8FD | CH48FD | ch4 8fd | ch48fd | Flintshire | Sir Y Fflint | Queensferry WwTW | 6273 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337537 | 364956 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8FE | CH48FE | ch4 8fe | ch48fe | Flintshire | Sir Y Fflint | Queensferry WwTW | 6291 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337539 | 364927 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8FF | CH48FF | ch4 8ff | ch48ff | Flintshire | Sir Y Fflint | Queensferry WwTW | 6249 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337438 | 364857 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8FG | CH48FG | ch4 8fg | ch48fg | Flintshire | Sir Y Fflint | Lavister WwTW | 6684 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338563 | 365147 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8GA | CH48GA | ch4 8ga | ch48ga | Flintshire | Sir Y Fflint | Lavister WwTW | 6723 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338584 | 365183 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8LA | CH48LA | ch4 8la | ch48la | Flintshire | Sir Y Fflint | Lavister WwTW | 6229 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338279 | 364720 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8LH | CH48LH | ch4 8lh | ch48lh | Flintshire | Sir Y Fflint | Lavister WwTW | 6268 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338251 | 364762 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8LQ | CH48LQ | ch4 8lq | ch48lq | Flintshire | Sir Y Fflint | Lavister WwTW | 5735 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338011 | 364244 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8LR | CH48LR | ch4 8lr | ch48lr | Flintshire | Sir Y Fflint | Lavister WwTW | 6329 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338325 | 364816 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8LT | CH48LT | ch4 8lt | ch48lt | Flintshire | Sir Y Fflint | Lavister WwTW | 6325 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338238 | 364820 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8LW | CH48LW | ch4 8lw | ch48lw | Flintshire | Sir Y Fflint | Lavister WwTW | 5784 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338104 | 364288 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8NA | CH48NA | ch4 8na | ch48na | Flintshire | Sir Y Fflint | Lavister WwTW | 6143 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338235 | 364638 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8NB | CH48NB | ch4 8nb | ch48nb | Flintshire | Sir Y Fflint | Lavister WwTW | 6057 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338243 | 364551 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8NH | CH48NH | ch4 8nh | ch48nh | Flintshire | Sir Y Fflint | Lavister WwTW | 6489 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338535 | 364954 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8PB | CH48PB | ch4 8pb | ch48pb | Flintshire | Sir Y Fflint | Lavister WwTW | 6136 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338317 | 364623 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8PY | CH48PY | ch4 8py | ch48py | Flintshire | Sir Y Fflint | Lavister WwTW | 6180 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338376 | 364661 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QB | CH48QB | ch4 8qb | ch48qb | Flintshire | Sir Y Fflint | Lavister WwTW | 6409 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338263 | 364902 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QE | CH48QE | ch4 8qe | ch48qe | Flintshire | Sir Y Fflint | Lavister WwTW | 6272 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338355 | 364756 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QF | CH48QF | ch4 8qf | ch48qf | Flintshire | Sir Y Fflint | Lavister WwTW | 6451 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338500 | 364920 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QG | CH48QG | ch4 8qg | ch48qg | Flintshire | Sir Y Fflint | Lavister WwTW | 6353 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338465 | 364825 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QH | CH48QH | ch4 8qh | ch48qh | Flintshire | Sir Y Fflint | Lavister WwTW | 6333 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338400 | 364813 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QJ | CH48QJ | ch4 8qj | ch48qj | Flintshire | Sir Y Fflint | Lavister WwTW | 6303 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338489 | 364772 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QL | CH48QL | ch4 8ql | ch48ql | Flintshire | Sir Y Fflint | Lavister WwTW | 6352 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338511 | 364819 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QN | CH48QN | ch4 8qn | ch48qn | Flintshire | Sir Y Fflint | Lavister WwTW | 5990 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337714 | 364507 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QP | CH48QP | ch4 8qp | ch48qp | Flintshire | Sir Y Fflint | Lavister WwTW | 5810 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337741 | 364327 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QQ | CH48QQ | ch4 8qq | ch48qq | Flintshire | Sir Y Fflint | Lavister WwTW | 6284 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338435 | 364759 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QR | CH48QR | ch4 8qr | ch48qr | Flintshire | Sir Y Fflint | Lavister WwTW | 5787 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337794 | 364303 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QS | CH48QS | ch4 8qs | ch48qs | Flintshire | Sir Y Fflint | Lavister WwTW | 6262 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338403 | 364741 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QT | CH48QT | ch4 8qt | ch48qt | Flintshire | Sir Y Fflint | Lavister WwTW | 6254 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338458 | 364726 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QW | CH48QW | ch4 8qw | ch48qw | Flintshire | Sir Y Fflint | Lavister WwTW | 6019 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337702 | 364536 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8QZ | CH48QZ | ch4 8qz | ch48qz | Flintshire | Sir Y Fflint | Lavister WwTW | 6519 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338421 | 364997 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8RB | CH48RB | ch4 8rb | ch48rb | Flintshire | Sir Y Fflint | Lavister WwTW | 6740 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338362 | 365225 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8RF | CH48RF | ch4 8rf | ch48rf | Flintshire | Sir Y Fflint | Queensferry WwTW | 6180 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337581 | 365189 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8RG | CH48RG | ch4 8rg | ch48rg | Flintshire | Sir Y Fflint | Lavister WwTW | 6768 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338426 | 365247 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8RH | CH48RH | ch4 8rh | ch48rh | Flintshire | Sir Y Fflint | Queensferry WwTW | 6791 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338366 | 365321 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8RJ | CH48RJ | ch4 8rj | ch48rj | Flintshire | Sir Y Fflint | Queensferry WwTW | 6008 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337399 | 365225 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8RL | CH48RL | ch4 8rl | ch48rl | Flintshire | Sir Y Fflint | Lavister WwTW | 6882 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338503 | 365353 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8RQ | CH48RQ | ch4 8rq | ch48rq | Flintshire | Sir Y Fflint | Queensferry WwTW | 6473 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337908 | 365161 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8RR | CH48RR | ch4 8rr | ch48rr | Flintshire | Sir Y Fflint | Lavister WwTW | 5919 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337936 | 364432 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8RS | CH48RS | ch4 8rs | ch48rs | Flintshire | Sir Y Fflint | Queensferry WwTW | 5955 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337418 | 365352 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8RT | CH48RT | ch4 8rt | ch48rt | Flintshire | Sir Y Fflint | Lavister WwTW | 5812 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337948 | 364324 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8RU | CH48RU | ch4 8ru | ch48ru | Flintshire | Sir Y Fflint | Queensferry WwTW | 6296 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337584 | 364983 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8RW | CH48RW | ch4 8rw | ch48rw | Flintshire | Sir Y Fflint | Queensferry WwTW | 6249 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337552 | 365020 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SB | CH48SB | ch4 8sb | ch48sb | Flintshire | Sir Y Fflint | Queensferry WwTW | 6720 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338232 | 365225 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SE | CH48SE | ch4 8se | ch48se | Flintshire | Sir Y Fflint | Lavister WwTW | 6621 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338508 | 365090 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SF | CH48SF | ch4 8sf | ch48sf | Flintshire | Sir Y Fflint | Lavister WwTW | 6567 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338332 | 365055 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SG | CH48SG | ch4 8sg | ch48sg | Flintshire | Sir Y Fflint | Lavister WwTW | 6465 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338148 | 364967 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SH | CH48SH | ch4 8sh | ch48sh | Flintshire | Sir Y Fflint | Lavister WwTW | 6351 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337851 | 364866 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SJ | CH48SJ | ch4 8sj | ch48sj | Flintshire | Sir Y Fflint | Lavister WwTW | 6405 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337910 | 364919 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SL | CH48SL | ch4 8sl | ch48sl | Flintshire | Sir Y Fflint | Queensferry WwTW | 6155 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337534 | 365162 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SN | CH48SN | ch4 8sn | ch48sn | Flintshire | Sir Y Fflint | Queensferry WwTW | 6512 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337876 | 365035 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SQ | CH48SQ | ch4 8sq | ch48sq | Flintshire | Sir Y Fflint | Lavister WwTW | 6488 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338107 | 364993 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SS | CH48SS | ch4 8ss | ch48ss | Flintshire | Sir Y Fflint | Lavister WwTW | 6246 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337912 | 364760 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8ST | CH48ST | ch4 8st | ch48st | Flintshire | Sir Y Fflint | Lavister WwTW | 6238 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337942 | 364751 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SU | CH48SU | ch4 8su | ch48su | Flintshire | Sir Y Fflint | Lavister WwTW | 6196 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337858 | 364711 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SW | CH48SW | ch4 8sw | ch48sw | Flintshire | Sir Y Fflint | Lavister WwTW | 6579 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338145 | 365082 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SX | CH48SX | ch4 8sx | ch48sx | Flintshire | Sir Y Fflint | Lavister WwTW | 6615 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338306 | 365105 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SY | CH48SY | ch4 8sy | ch48sy | Flintshire | Sir Y Fflint | Lavister WwTW | 5833 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337912 | 364347 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8SZ | CH48SZ | ch4 8sz | ch48sz | Flintshire | Sir Y Fflint | Lavister WwTW | 5853 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337878 | 364368 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TB | CH48TB | ch4 8tb | ch48tb | Flintshire | Sir Y Fflint | Lavister WwTW | 6212 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337998 | 364722 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TD | CH48TD | ch4 8td | ch48td | Flintshire | Sir Y Fflint | Lavister WwTW | 6258 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337963 | 364770 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TE | CH48TE | ch4 8te | ch48te | Flintshire | Sir Y Fflint | Lavister WwTW | 6354 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337996 | 364865 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TF | CH48TF | ch4 8tf | ch48tf | Flintshire | Sir Y Fflint | Lavister WwTW | 6399 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338141 | 364902 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TG | CH48TG | ch4 8tg | ch48tg | Flintshire | Sir Y Fflint | Lavister WwTW | 6134 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338021 | 364643 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TH | CH48TH | ch4 8th | ch48th | Flintshire | Sir Y Fflint | Lavister WwTW | 5974 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338067 | 364481 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TJ | CH48TJ | ch4 8tj | ch48tj | Flintshire | Sir Y Fflint | Lavister WwTW | 5844 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337962 | 364356 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TL | CH48TL | ch4 8tl | ch48tl | Flintshire | Sir Y Fflint | Lavister WwTW | 5974 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338122 | 364477 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TN | CH48TN | ch4 8tn | ch48tn | Flintshire | Sir Y Fflint | Lavister WwTW | 5831 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338081 | 364336 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TP | CH48TP | ch4 8tp | ch48tp | Flintshire | Sir Y Fflint | Lavister WwTW | 6384 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338221 | 364881 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TQ | CH48TQ | ch4 8tq | ch48tq | Flintshire | Sir Y Fflint | Lavister WwTW | 6028 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338036 | 364536 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TR | CH48TR | ch4 8tr | ch48tr | Flintshire | Sir Y Fflint | Lavister WwTW | 6167 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338140 | 364669 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TS | CH48TS | ch4 8ts | ch48ts | Flintshire | Sir Y Fflint | Lavister WwTW | 6146 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338108 | 364650 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TT | CH48TT | ch4 8tt | ch48tt | Flintshire | Sir Y Fflint | Lavister WwTW | 6408 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338085 | 364914 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TU | CH48TU | ch4 8tu | ch48tu | Flintshire | Sir Y Fflint | Lavister WwTW | 6104 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338056 | 364611 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TW | CH48TW | ch4 8tw | ch48tw | Flintshire | Sir Y Fflint | Lavister WwTW | 5816 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338009 | 364326 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TX | CH48TX | ch4 8tx | ch48tx | Flintshire | Sir Y Fflint | Lavister WwTW | 6036 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338079 | 364542 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TY | CH48TY | ch4 8ty | ch48ty | Flintshire | Sir Y Fflint | Lavister WwTW | 6175 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338038 | 364683 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8TZ | CH48TZ | ch4 8tz | ch48tz | Flintshire | Sir Y Fflint | Lavister WwTW | 6257 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 338020 | 364766 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8UA | CH48UA | ch4 8ua | ch48ua | Flintshire | Sir Y Fflint | Lavister WwTW | 5685 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337756 | 364202 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8UB | CH48UB | ch4 8ub | ch48ub | Flintshire | Sir Y Fflint | Lavister WwTW | 6087 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337577 | 364602 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8UD | CH48UD | ch4 8ud | ch48ud | Flintshire | Sir Y Fflint | Lavister WwTW | 6137 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337665 | 364654 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8UE | CH48UE | ch4 8ue | ch48ue | Flintshire | Sir Y Fflint | Lavister WwTW | 6239 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337587 | 364754 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8UF | CH48UF | ch4 8uf | ch48uf | Flintshire | Sir Y Fflint | Lavister WwTW | 6233 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337641 | 364749 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8UG | CH48UG | ch4 8ug | ch48ug | Flintshire | Sir Y Fflint | Lavister WwTW | 6086 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337862 | 364601 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8UH | CH48UH | ch4 8uh | ch48uh | Flintshire | Sir Y Fflint | Lavister WwTW | 6287 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337781 | 364803 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8UJ | CH48UJ | ch4 8uj | ch48uj | Flintshire | Sir Y Fflint | Lavister WwTW | 5918 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337779 | 364435 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8UL | CH48UL | ch4 8ul | ch48ul | Flintshire | Sir Y Fflint | Lavister WwTW | 5935 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337739 | 364452 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8UP | CH48UP | ch4 8up | ch48up | Flintshire | Sir Y Fflint | Lavister WwTW | 5635 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337816 | 364151 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8UQ | CH48UQ | ch4 8uq | ch48uq | Flintshire | Sir Y Fflint | Lavister WwTW | 6089 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337924 | 364602 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 8UT | CH48UT | ch4 8ut | ch48ut | Flintshire | Sir Y Fflint | Lavister WwTW | 6366 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337934 | 364879 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AA | CH49AA | ch4 9aa | ch49aa | Flintshire | Sir Y Fflint | Hope WwTW | 4193 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 332970 | 361523 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AB | CH49AB | ch4 9ab | ch49ab | Flintshire | Sir Y Fflint | Hope WwTW | 3827 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 332926 | 361101 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AH | CH49AH | ch4 9ah | ch49ah | Flintshire | Sir Y Fflint | Lavister WwTW | 3786 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 334564 | 360615 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AJ | CH49AJ | ch4 9aj | ch49aj | Flintshire | Sir Y Fflint | Hope WwTW | 3853 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 332883 | 361166 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AL | CH49AL | ch4 9al | ch49al | Flintshire | Sir Y Fflint | Hope WwTW | 4303 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 333127 | 361546 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AN | CH49AN | ch4 9an | ch49an | Flintshire | Sir Y Fflint | Hope WwTW | 2552 | 792 | 700to900 | 1.59 | 1.16 | 0.85 | 14.76 | 7.87 | 8.7 | 332061 | 360157 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AP | CH49AP | ch4 9ap | ch49ap | Flintshire | Sir Y Fflint | Hope WwTW | 3142 | 782 | 700to900 | 1.57 | 1.15 | 0.84 | 14.58 | 7.77 | 8.59 | 332444 | 360608 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AQ | CH49AQ | ch4 9aq | ch49aq | Flintshire | Sir Y Fflint | Lavister WwTW | 4649 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 334546 | 361918 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AR | CH49AR | ch4 9ar | ch49ar | Flintshire | Sir Y Fflint | Hope WwTW | 3910 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 332997 | 361150 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AS | CH49AS | ch4 9as | ch49as | Flintshire | Sir Y Fflint | Hope WwTW | 3976 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 332864 | 361333 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AT | CH49AT | ch4 9at | ch49at | Flintshire | Sir Y Fflint | Hope WwTW | 3940 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 332809 | 361328 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AU | CH49AU | ch4 9au | ch49au | Flintshire | Sir Y Fflint | Hope WwTW | 2334 | 792 | 700to900 | 1.59 | 1.16 | 0.85 | 14.76 | 7.87 | 8.7 | 331574 | 360195 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AW | CH49AW | ch4 9aw | ch49aw | Flintshire | Sir Y Fflint | Hope WwTW | 2878 | 792 | 700to900 | 1.59 | 1.16 | 0.85 | 14.76 | 7.87 | 8.7 | 332429 | 360282 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AX | CH49AX | ch4 9ax | ch49ax | Flintshire | Sir Y Fflint | Hope WwTW | 3162 | 782 | 700to900 | 1.57 | 1.15 | 0.84 | 14.58 | 7.77 | 8.59 | 331976 | 360920 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AY | CH49AY | ch4 9ay | ch49ay | Flintshire | Sir Y Fflint | Hope WwTW | 4058 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333067 | 361284 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9AZ | CH49AZ | ch4 9az | ch49az | Flintshire | Sir Y Fflint | Hope WwTW | 4129 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333151 | 361307 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BA | CH49BA | ch4 9ba | ch49ba | Flintshire | Sir Y Fflint | Hope WwTW | 3996 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333007 | 361252 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BB | CH49BB | ch4 9bb | ch49bb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3968 | 778 | 700to900 | 1.56 | 1.14 | 0.84 | 14.5 | 7.73 | 8.55 | 331856 | 362131 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BE | CH49BE | ch4 9be | ch49be | Flintshire | Sir Y Fflint | Hope WwTW | 4198 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 332613 | 361754 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BF | CH49BF | ch4 9bf | ch49bf | Flintshire | Sir Y Fflint | Hope WwTW | 4332 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 333124 | 361584 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BG | CH49BG | ch4 9bg | ch49bg | Flintshire | Sir Y Fflint | Hope WwTW | 4332 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 333079 | 361617 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BH | CH49BH | ch4 9bh | ch49bh | Flintshire | Sir Y Fflint | Hope WwTW | 3927 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333099 | 361089 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BJ | CH49BJ | ch4 9bj | ch49bj | Flintshire | Sir Y Fflint | Hope WwTW | 3467 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 333175 | 360370 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BL | CH49BL | ch4 9bl | ch49bl | Flintshire | Sir Y Fflint | Hope WwTW | 3469 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 333148 | 360403 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BN | CH49BN | ch4 9bn | ch49bn | Flintshire | Sir Y Fflint | Hope WwTW | 3802 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 332798 | 361166 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BP | CH49BP | ch4 9bp | ch49bp | Flintshire | Sir Y Fflint | Hope WwTW | 3119 | 763 | 700to900 | 1.53 | 1.12 | 0.82 | 14.22 | 7.58 | 8.38 | 333309 | 359569 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BQ | CH49BQ | ch4 9bq | ch49bq | Flintshire | Sir Y Fflint | Hope WwTW | 4618 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 332908 | 362069 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BR | CH49BR | ch4 9br | ch49br | Flintshire | Sir Y Fflint | Hope WwTW | 4063 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 333817 | 360522 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BS | CH49BS | ch4 9bs | ch49bs | Flintshire | Sir Y Fflint | Hope WwTW | 3646 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333201 | 360607 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BT | CH49BT | ch4 9bt | ch49bt | Flintshire | Sir Y Fflint | Hope WwTW | 4260 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333220 | 361420 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BU | CH49BU | ch4 9bu | ch49bu | Flintshire | Sir Y Fflint | Hope WwTW | 4231 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333211 | 361390 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BX | CH49BX | ch4 9bx | ch49bx | Flintshire | Sir Y Fflint | Hope WwTW | 4242 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333290 | 361339 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BY | CH49BY | ch4 9by | ch49by | Flintshire | Sir Y Fflint | Hope WwTW | 4267 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 333050 | 361557 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9BZ | CH49BZ | ch4 9bz | ch49bz | Flintshire | Sir Y Fflint | Hope WwTW | 4411 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 333667 | 361224 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9DA | CH49DA | ch4 9da | ch49da | Flintshire | Sir Y Fflint | Hope WwTW | 4248 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333260 | 361372 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9DB | CH49DB | ch4 9db | ch49db | Flintshire | Sir Y Fflint | Hope WwTW | 4093 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 333617 | 360815 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9DX | CH49DX | ch4 9dx | ch49dx | Flintshire | Sir Y Fflint | Hope WwTW | 4166 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333184 | 361328 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9DY | CH49DY | ch4 9dy | ch49dy | Flintshire | Sir Y Fflint | Hope WwTW | 3980 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333109 | 361150 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9DZ | CH49DZ | ch4 9dz | ch49dz | Flintshire | Sir Y Fflint | Hope WwTW | 4322 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333237 | 361486 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9EA | CH49EA | ch4 9ea | ch49ea | Flintshire | Sir Y Fflint | Hope WwTW | 4147 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333251 | 361248 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9EH | CH49EH | ch4 9eh | ch49eh | Flintshire | Sir Y Fflint | Hope WwTW | 4071 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 333208 | 361185 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9FW | CH49FW | ch4 9fw | ch49fw | Flintshire | Sir Y Fflint | Hope WwTW | 4277 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 332902 | 361671 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9FX | CH49FX | ch4 9fx | ch49fx | Flintshire | Sir Y Fflint | Hope WwTW | 4289 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 332984 | 361631 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9GD | CH49GD | ch4 9gd | ch49gd | Flintshire | Sir Y Fflint | Hope WwTW | 3632 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 332824 | 360933 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9GF | CH49GF | ch4 9gf | ch49gf | Flintshire | Sir Y Fflint | Hope WwTW | 4229 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 332915 | 361605 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9GG | CH49GG | ch4 9gg | ch49gg | Flintshire | Sir Y Fflint | Hope WwTW | 4249 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 332848 | 361673 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9GW | CH49GW | ch4 9gw | ch49gw | Flintshire | Sir Y Fflint | Hope WwTW | 4322 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 333009 | 361654 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9PA | CH49PA | ch4 9pa | ch49pa | Flintshire | Sir Y Fflint | Hope WwTW | 4054 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 332883 | 361415 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9PB | CH49PB | ch4 9pb | ch49pb | Flintshire | Sir Y Fflint | Hope WwTW | 4104 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 332973 | 361412 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9PD | CH49PD | ch4 9pd | ch49pd | Flintshire | Sir Y Fflint | Hope WwTW | 4136 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 332942 | 361473 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9PF | CH49PF | ch4 9pf | ch49pf | Flintshire | Sir Y Fflint | Hope WwTW | 3752 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 332921 | 361009 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH4 9PG | CH49PG | ch4 9pg | ch49pg | Flintshire | Sir Y Fflint | Hope WwTW | 3756 | 756 | 700to900 | 1.51 | 1.11 | 0.81 | 14.09 | 7.52 | 8.31 | 332942 | 360997 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AB | CH51AB | ch5 1ab | ch51ab | Flintshire | Sir Y Fflint | Connahs Quay STW | 846 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330866 | 368811 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AD | CH51AD | ch5 1ad | ch51ad | Flintshire | Sir Y Fflint | Connahs Quay STW | 977 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330883 | 368645 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AE | CH51AE | ch5 1ae | ch51ae | Flintshire | Sir Y Fflint | Connahs Quay STW | 1203 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330979 | 368431 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AF | CH51AF | ch5 1af | ch51af | Flintshire | Sir Y Fflint | Connahs Quay STW | 852 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330893 | 368833 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AG | CH51AG | ch5 1ag | ch51ag | Flintshire | Sir Y Fflint | Connahs Quay STW | 880 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330933 | 368838 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AH | CH51AH | ch5 1ah | ch51ah | Flintshire | Sir Y Fflint | Connahs Quay STW | 989 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330850 | 368602 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AJ | CH51AJ | ch5 1aj | ch51aj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1027 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330795 | 368516 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AL | CH51AL | ch5 1al | ch51al | Flintshire | Sir Y Fflint | Connahs Quay STW | 1073 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330680 | 368402 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AN | CH51AN | ch5 1an | ch51an | Flintshire | Sir Y Fflint | Connahs Quay STW | 1026 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330684 | 368455 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AP | CH51AP | ch5 1ap | ch51ap | Flintshire | Sir Y Fflint | Connahs Quay STW | 1036 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330774 | 368493 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AQ | CH51AQ | ch5 1aq | ch51aq | Flintshire | Sir Y Fflint | Connahs Quay STW | 826 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330931 | 368928 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AR | CH51AR | ch5 1ar | ch51ar | Flintshire | Sir Y Fflint | Connahs Quay STW | 958 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330726 | 368555 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AS | CH51AS | ch5 1as | ch51as | Flintshire | Sir Y Fflint | Connahs Quay STW | 1066 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330572 | 368367 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AT | CH51AT | ch5 1at | ch51at | Flintshire | Sir Y Fflint | Connahs Quay STW | 868 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330780 | 368701 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AU | CH51AU | ch5 1au | ch51au | Flintshire | Sir Y Fflint | Connahs Quay STW | 802 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330693 | 368718 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AW | CH51AW | ch5 1aw | ch51aw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1068 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330757 | 368446 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AX | CH51AX | ch5 1ax | ch51ax | Flintshire | Sir Y Fflint | Connahs Quay STW | 891 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330577 | 368556 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AY | CH51AY | ch5 1ay | ch51ay | Flintshire | Sir Y Fflint | Connahs Quay STW | 999 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330503 | 368417 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1AZ | CH51AZ | ch5 1az | ch51az | Flintshire | Sir Y Fflint | Connahs Quay STW | 874 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330710 | 368643 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BA | CH51BA | ch5 1ba | ch51ba | Flintshire | Sir Y Fflint | Connahs Quay STW | 908 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330682 | 368587 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BB | CH51BB | ch5 1bb | ch51bb | Flintshire | Sir Y Fflint | Connahs Quay STW | 912 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330650 | 368566 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BD | CH51BD | ch5 1bd | ch51bd | Flintshire | Sir Y Fflint | Connahs Quay STW | 957 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330603 | 368495 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BE | CH51BE | ch5 1be | ch51be | Flintshire | Sir Y Fflint | Connahs Quay STW | 983 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330587 | 368461 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BF | CH51BF | ch5 1bf | ch51bf | Flintshire | Sir Y Fflint | Connahs Quay STW | 937 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330842 | 368662 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BG | CH51BG | ch5 1bg | ch51bg | Flintshire | Sir Y Fflint | Connahs Quay STW | 1039 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330544 | 368387 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BH | CH51BH | ch5 1bh | ch51bh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1073 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330492 | 368337 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BJ | CH51BJ | ch5 1bj | ch51bj | Flintshire | Sir Y Fflint | Connahs Quay STW | 970 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330776 | 368572 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BL | CH51BL | ch5 1bl | ch51bl | Flintshire | Sir Y Fflint | Connahs Quay STW | 1657 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330265 | 367724 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BN | CH51BN | ch5 1bn | ch51bn | Flintshire | Sir Y Fflint | Connahs Quay STW | 1586 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330255 | 367795 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BP | CH51BP | ch5 1bp | ch51bp | Flintshire | Sir Y Fflint | Connahs Quay STW | 1192 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330993 | 368456 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BQ | CH51BQ | ch5 1bq | ch51bq | Flintshire | Sir Y Fflint | Connahs Quay STW | 999 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330464 | 368407 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BR | CH51BR | ch5 1br | ch51br | Flintshire | Sir Y Fflint | Connahs Quay STW | 1163 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330939 | 368451 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BX | CH51BX | ch5 1bx | ch51bx | Flintshire | Sir Y Fflint | Connahs Quay STW | 696 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330678 | 368839 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BY | CH51BY | ch5 1by | ch51by | Flintshire | Sir Y Fflint | Connahs Quay STW | 530 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330558 | 368956 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1BZ | CH51BZ | ch5 1bz | ch51bz | Flintshire | Sir Y Fflint | Connahs Quay STW | 433 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330434 | 368993 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DE | CH51DE | ch5 1de | ch51de | Flintshire | Sir Y Fflint | Connahs Quay STW | 605 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330602 | 368895 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DF | CH51DF | ch5 1df | ch51df | Flintshire | Sir Y Fflint | Connahs Quay STW | 671 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330657 | 368854 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DH | CH51DH | ch5 1dh | ch51dh | Flintshire | Sir Y Fflint | Connahs Quay STW | 743 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330822 | 368919 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DJ | CH51DJ | ch5 1dj | ch51dj | Flintshire | Sir Y Fflint | Connahs Quay STW | 770 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330828 | 368884 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DL | CH51DL | ch5 1dl | ch51dl | Flintshire | Sir Y Fflint | Connahs Quay STW | 641 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330733 | 368971 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DN | CH51DN | ch5 1dn | ch51dn | Flintshire | Sir Y Fflint | Connahs Quay STW | 573 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330666 | 368997 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DP | CH51DP | ch5 1dp | ch51dp | Flintshire | Sir Y Fflint | Connahs Quay STW | 499 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330596 | 369030 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DQ | CH51DQ | ch5 1dq | ch51dq | Flintshire | Sir Y Fflint | Connahs Quay STW | 800 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330894 | 368919 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DR | CH51DR | ch5 1dr | ch51dr | Flintshire | Sir Y Fflint | Connahs Quay STW | 527 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330626 | 369022 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DT | CH51DT | ch5 1dt | ch51dt | Flintshire | Sir Y Fflint | Connahs Quay STW | 465 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330544 | 369029 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DU | CH51DU | ch5 1du | ch51du | Flintshire | Sir Y Fflint | Connahs Quay STW | 357 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330468 | 369105 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DW | CH51DW | ch5 1dw | ch51dw | Flintshire | Sir Y Fflint | Connahs Quay STW | 598 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330698 | 368996 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DX | CH51DX | ch5 1dx | ch51dx | Flintshire | Sir Y Fflint | Connahs Quay STW | 454 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330598 | 369101 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DY | CH51DY | ch5 1dy | ch51dy | Flintshire | Sir Y Fflint | Connahs Quay STW | 685 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330556 | 368772 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1DZ | CH51DZ | ch5 1dz | ch51dz | Flintshire | Sir Y Fflint | Connahs Quay STW | 765 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330453 | 368646 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1EA | CH51EA | ch5 1ea | ch51ea | Flintshire | Sir Y Fflint | Connahs Quay STW | 874 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330346 | 368513 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1EB | CH51EB | ch5 1eb | ch51eb | Flintshire | Sir Y Fflint | Connahs Quay STW | 703 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330628 | 368794 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1ED | CH51ED | ch5 1ed | ch51ed | Flintshire | Sir Y Fflint | Connahs Quay STW | 330 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330476 | 369149 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1EF | CH51EF | ch5 1ef | ch51ef | Flintshire | Sir Y Fflint | Connahs Quay STW | 1003 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330301 | 368379 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1EH | CH51EH | ch5 1eh | ch51eh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1263 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331056 | 368417 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1ES | CH51ES | ch5 1es | ch51es | Flintshire | Sir Y Fflint | Connahs Quay STW | 502 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330431 | 368916 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1EY | CH51EY | ch5 1ey | ch51ey | Flintshire | Sir Y Fflint | Connahs Quay STW | 531 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330458 | 368896 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1EZ | CH51EZ | ch5 1ez | ch51ez | Flintshire | Sir Y Fflint | Connahs Quay STW | 565 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330428 | 368847 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HA | CH51HA | ch5 1ha | ch51ha | Flintshire | Sir Y Fflint | Connahs Quay STW | 571 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330353 | 368820 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HB | CH51HB | ch5 1hb | ch51hb | Flintshire | Sir Y Fflint | Connahs Quay STW | 572 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330391 | 368828 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HE | CH51HE | ch5 1he | ch51he | Flintshire | Sir Y Fflint | Connahs Quay STW | 611 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330360 | 368781 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HF | CH51HF | ch5 1hf | ch51hf | Flintshire | Sir Y Fflint | Connahs Quay STW | 584 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330335 | 368804 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HG | CH51HG | ch5 1hg | ch51hg | Flintshire | Sir Y Fflint | Connahs Quay STW | 526 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330268 | 368855 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HH | CH51HH | ch5 1hh | ch51hh | Flintshire | Sir Y Fflint | Connahs Quay STW | 430 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330272 | 368951 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HJ | CH51HJ | ch5 1hj | ch51hj | Flintshire | Sir Y Fflint | Connahs Quay STW | 526 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330216 | 368855 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HL | CH51HL | ch5 1hl | ch51hl | Flintshire | Sir Y Fflint | Connahs Quay STW | 524 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330197 | 368858 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HN | CH51HN | ch5 1hn | ch51hn | Flintshire | Sir Y Fflint | Connahs Quay STW | 600 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330197 | 368782 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HP | CH51HP | ch5 1hp | ch51hp | Flintshire | Sir Y Fflint | Connahs Quay STW | 897 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330167 | 368486 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HQ | CH51HQ | ch5 1hq | ch51hq | Flintshire | Sir Y Fflint | Connahs Quay STW | 466 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330359 | 368930 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HR | CH51HR | ch5 1hr | ch51hr | Flintshire | Sir Y Fflint | Connahs Quay STW | 611 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330233 | 368769 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HS | CH51HS | ch5 1hs | ch51hs | Flintshire | Sir Y Fflint | Connahs Quay STW | 722 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330173 | 368661 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HT | CH51HT | ch5 1ht | ch51ht | Flintshire | Sir Y Fflint | Connahs Quay STW | 685 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330267 | 368696 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HU | CH51HU | ch5 1hu | ch51hu | Flintshire | Sir Y Fflint | Connahs Quay STW | 763 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330221 | 368617 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HW | CH51HW | ch5 1hw | ch51hw | Flintshire | Sir Y Fflint | Connahs Quay STW | 611 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330296 | 368772 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HX | CH51HX | ch5 1hx | ch51hx | Flintshire | Sir Y Fflint | Connahs Quay STW | 809 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330144 | 368577 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HY | CH51HY | ch5 1hy | ch51hy | Flintshire | Sir Y Fflint | Connahs Quay STW | 796 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330177 | 368587 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1HZ | CH51HZ | ch5 1hz | ch51hz | Flintshire | Sir Y Fflint | Connahs Quay STW | 735 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330378 | 368658 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1JA | CH51JA | ch5 1ja | ch51ja | Flintshire | Sir Y Fflint | Connahs Quay STW | 676 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330394 | 368722 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1JB | CH51JB | ch5 1jb | ch51jb | Flintshire | Sir Y Fflint | Connahs Quay STW | 609 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330501 | 368830 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1JJ | CH51JJ | ch5 1jj | ch51jj | Flintshire | Sir Y Fflint | Queensferry WwTW | 1098 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 331282 | 368547 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1JP | CH51JP | ch5 1jp | ch51jp | Flintshire | Sir Y Fflint | Connahs Quay STW | 1216 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330787 | 368294 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1JR | CH51JR | ch5 1jr | ch51jr | Flintshire | Sir Y Fflint | Connahs Quay STW | 1390 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330975 | 368201 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1JS | CH51JS | ch5 1js | ch51js | Flintshire | Sir Y Fflint | Connahs Quay STW | 1386 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330997 | 368220 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1JT | CH51JT | ch5 1jt | ch51jt | Flintshire | Sir Y Fflint | Queensferry WwTW | 1299 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331153 | 368095 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1JU | CH51JU | ch5 1ju | ch51ju | Flintshire | Sir Y Fflint | Queensferry WwTW | 1353 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331135 | 367990 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1JW | CH51JW | ch5 1jw | ch51jw | Flintshire | Sir Y Fflint | Connahs Quay STW | 620 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330514 | 368824 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1JX | CH51JX | ch5 1jx | ch51jx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1322 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331015 | 368309 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1JY | CH51JY | ch5 1jy | ch51jy | Flintshire | Sir Y Fflint | Queensferry WwTW | 1358 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331049 | 368251 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1JZ | CH51JZ | ch5 1jz | ch51jz | Flintshire | Sir Y Fflint | Queensferry WwTW | 1377 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331082 | 368062 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LA | CH51LA | ch5 1la | ch51la | Flintshire | Sir Y Fflint | Connahs Quay STW | 1235 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330748 | 368255 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LB | CH51LB | ch5 1lb | ch51lb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1389 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330934 | 368177 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LD | CH51LD | ch5 1ld | ch51ld | Flintshire | Sir Y Fflint | Connahs Quay STW | 1262 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330739 | 368221 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LE | CH51LE | ch5 1le | ch51le | Flintshire | Sir Y Fflint | Connahs Quay STW | 1421 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330932 | 368140 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LF | CH51LF | ch5 1lf | ch51lf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1421 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330874 | 368109 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LG | CH51LG | ch5 1lg | ch51lg | Flintshire | Sir Y Fflint | Queensferry WwTW | 1423 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331064 | 367980 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LH | CH51LH | ch5 1lh | ch51lh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1342 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330787 | 368155 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LJ | CH51LJ | ch5 1lj | ch51lj | Flintshire | Sir Y Fflint | Queensferry WwTW | 1521 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330943 | 368021 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LL | CH51LL | ch5 1ll | ch51ll | Flintshire | Sir Y Fflint | Queensferry WwTW | 1413 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331107 | 367908 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LN | CH51LN | ch5 1ln | ch51ln | Flintshire | Sir Y Fflint | Queensferry WwTW | 1624 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330916 | 367819 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LP | CH51LP | ch5 1lp | ch51lp | Flintshire | Sir Y Fflint | Connahs Quay STW | 1743 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330760 | 367717 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LQ | CH51LQ | ch5 1lq | ch51lq | Flintshire | Sir Y Fflint | Queensferry WwTW | 1378 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331161 | 367878 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LR | CH51LR | ch5 1lr | ch51lr | Flintshire | Sir Y Fflint | Connahs Quay STW | 1581 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330751 | 367884 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LS | CH51LS | ch5 1ls | ch51ls | Flintshire | Sir Y Fflint | Connahs Quay STW | 1443 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330608 | 367985 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LT | CH51LT | ch5 1lt | ch51lt | Flintshire | Sir Y Fflint | Connahs Quay STW | 1643 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330838 | 367850 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LU | CH51LU | ch5 1lu | ch51lu | Flintshire | Sir Y Fflint | Connahs Quay STW | 1403 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330640 | 368036 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LW | CH51LW | ch5 1lw | ch51lw | Flintshire | Sir Y Fflint | Queensferry WwTW | 1579 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330934 | 367886 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LX | CH51LX | ch5 1lx | ch51lx | Flintshire | Sir Y Fflint | Queensferry WwTW | 1524 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330967 | 367949 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1LZ | CH51LZ | ch5 1lz | ch51lz | Flintshire | Sir Y Fflint | Connahs Quay STW | 1315 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330748 | 368168 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NA | CH51NA | ch5 1na | ch51na | Flintshire | Sir Y Fflint | Connahs Quay STW | 1617 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330621 | 367809 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1ND | CH51ND | ch5 1nd | ch51nd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1665 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330700 | 367780 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NE | CH51NE | ch5 1ne | ch51ne | Flintshire | Sir Y Fflint | Connahs Quay STW | 1613 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330738 | 367846 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NF | CH51NF | ch5 1nf | ch51nf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1643 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330721 | 367810 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NG | CH51NG | ch5 1ng | ch51ng | Flintshire | Sir Y Fflint | Connahs Quay STW | 1566 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330691 | 367881 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NH | CH51NH | ch5 1nh | ch51nh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1540 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330562 | 367875 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NJ | CH51NJ | ch5 1nj | ch51nj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1522 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330632 | 367910 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NL | CH51NL | ch5 1nl | ch51nl | Flintshire | Sir Y Fflint | Connahs Quay STW | 1516 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330591 | 367906 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NN | CH51NN | ch5 1nn | ch51nn | Flintshire | Sir Y Fflint | Connahs Quay STW | 1545 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330898 | 367983 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NQ | CH51NQ | ch5 1nq | ch51nq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1569 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330617 | 367857 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NS | CH51NS | ch5 1ns | ch51ns | Flintshire | Sir Y Fflint | Connahs Quay STW | 1448 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330835 | 368060 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NT | CH51NT | ch5 1nt | ch51nt | Flintshire | Sir Y Fflint | Connahs Quay STW | 1446 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330760 | 368031 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NU | CH51NU | ch5 1nu | ch51nu | Flintshire | Sir Y Fflint | Connahs Quay STW | 1354 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330739 | 368122 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NW | CH51NW | ch5 1nw | ch51nw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1523 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330508 | 367881 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NX | CH51NX | ch5 1nx | ch51nx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1401 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330741 | 368072 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NY | CH51NY | ch5 1ny | ch51ny | Flintshire | Sir Y Fflint | Connahs Quay STW | 1383 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330695 | 368074 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1NZ | CH51NZ | ch5 1nz | ch51nz | Flintshire | Sir Y Fflint | Connahs Quay STW | 1321 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330634 | 368120 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1PA | CH51PA | ch5 1pa | ch51pa | Flintshire | Sir Y Fflint | Connahs Quay STW | 1407 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330585 | 368016 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1PB | CH51PB | ch5 1pb | ch51pb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1392 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330549 | 368023 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1PD | CH51PD | ch5 1pd | ch51pd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1445 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330551 | 367969 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1PE | CH51PE | ch5 1pe | ch51pe | Flintshire | Sir Y Fflint | Connahs Quay STW | 896 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330415 | 368502 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1PF | CH51PF | ch5 1pf | ch51pf | Flintshire | Sir Y Fflint | Connahs Quay STW | 775 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330525 | 368660 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1PJ | CH51PJ | ch5 1pj | ch51pj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1458 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330458 | 367939 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1PL | CH51PL | ch5 1pl | ch51pl | Flintshire | Sir Y Fflint | Connahs Quay STW | 1513 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330413 | 367877 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1PN | CH51PN | ch5 1pn | ch51pn | Flintshire | Sir Y Fflint | Connahs Quay STW | 1401 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330483 | 368001 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1PP | CH51PP | ch5 1pp | ch51pp | Flintshire | Sir Y Fflint | Connahs Quay STW | 964 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330986 | 368770 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1PU | CH51PU | ch5 1pu | ch51pu | Flintshire | Sir Y Fflint | Connahs Quay STW | 907 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330935 | 368797 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1PY | CH51PY | ch5 1py | ch51py | Flintshire | Sir Y Fflint | Connahs Quay STW | 931 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 331134 | 369121 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1PZ | CH51PZ | ch5 1pz | ch51pz | Flintshire | Sir Y Fflint | Connahs Quay STW | 904 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330985 | 368868 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QA | CH51QA | ch5 1qa | ch51qa | Flintshire | Sir Y Fflint | Connahs Quay STW | 838 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330793 | 368751 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QB | CH51QB | ch5 1qb | ch51qb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1018 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330952 | 368653 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QD | CH51QD | ch5 1qd | ch51qd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1214 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 331090 | 368514 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QE | CH51QE | ch5 1qe | ch51qe | Flintshire | Sir Y Fflint | Connahs Quay STW | 1350 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330508 | 368057 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QF | CH51QF | ch5 1qf | ch51qf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1422 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330321 | 367961 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QJ | CH51QJ | ch5 1qj | ch51qj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1101 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 331139 | 368745 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QN | CH51QN | ch5 1qn | ch51qn | Flintshire | Sir Y Fflint | Connahs Quay STW | 1178 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 331129 | 368608 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QP | CH51QP | ch5 1qp | ch51qp | Flintshire | Sir Y Fflint | Connahs Quay STW | 1141 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330812 | 368393 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QQ | CH51QQ | ch5 1qq | ch51qq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1042 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330912 | 368584 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QR | CH51QR | ch5 1qr | ch51qr | Flintshire | Sir Y Fflint | Connahs Quay STW | 1258 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330624 | 368182 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QS | CH51QS | ch5 1qs | ch51qs | Flintshire | Sir Y Fflint | Connahs Quay STW | 1332 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330452 | 368065 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QT | CH51QT | ch5 1qt | ch51qt | Flintshire | Sir Y Fflint | Connahs Quay STW | 1058 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330855 | 368520 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QU | CH51QU | ch5 1qu | ch51qu | Flintshire | Sir Y Fflint | Connahs Quay STW | 1113 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 330933 | 368509 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QW | CH51QW | ch5 1qw | ch51qw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1084 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330823 | 368466 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QX | CH51QX | ch5 1qx | ch51qx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1069 | 730 | 700to900 | 1.46 | 1.07 | 0.78 | 13.6 | 7.25 | 8.02 | 331016 | 368646 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QY | CH51QY | ch5 1qy | ch51qy | Flintshire | Sir Y Fflint | Connahs Quay STW | 1273 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330424 | 368121 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1QZ | CH51QZ | ch5 1qz | ch51qz | Flintshire | Sir Y Fflint | Connahs Quay STW | 1237 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330366 | 368150 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1RA | CH51RA | ch5 1ra | ch51ra | Flintshire | Sir Y Fflint | Connahs Quay STW | 1326 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330424 | 368067 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1RB | CH51RB | ch5 1rb | ch51rb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1480 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330379 | 367907 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1RD | CH51RD | ch5 1rd | ch51rd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1425 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330378 | 367962 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1RE | CH51RE | ch5 1re | ch51re | Flintshire | Sir Y Fflint | Connahs Quay STW | 1384 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330374 | 368003 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1RF | CH51RF | ch5 1rf | ch51rf | Flintshire | Sir Y Fflint | Connahs Quay STW | 976 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330008 | 368432 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1SA | CH51SA | ch5 1sa | ch51sa | Flintshire | Sir Y Fflint | Queensferry WwTW | 890 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331547 | 368207 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1SF | CH51SF | ch5 1sf | ch51sf | Flintshire | Sir Y Fflint | Queensferry WwTW | 683 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 331729 | 368732 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1SR | CH51SR | ch5 1sr | ch51sr | Flintshire | Sir Y Fflint | Queensferry WwTW | 595 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331847 | 368256 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1SS | CH51SS | ch5 1ss | ch51ss | Flintshire | Sir Y Fflint | Queensferry WwTW | 729 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331684 | 368304 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1ST | CH51ST | ch5 1st | ch51st | Flintshire | Sir Y Fflint | Queensferry WwTW | 668 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331756 | 368281 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1SU | CH51SU | ch5 1su | ch51su | Flintshire | Sir Y Fflint | Queensferry WwTW | 684 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331761 | 368229 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1SW | CH51SW | ch5 1sw | ch51sw | Flintshire | Sir Y Fflint | Queensferry WwTW | 656 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331756 | 368318 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1SX | CH51SX | ch5 1sx | ch51sx | Flintshire | Sir Y Fflint | Queensferry WwTW | 667 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331788 | 368213 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1SY | CH51SY | ch5 1sy | ch51sy | Flintshire | Sir Y Fflint | Queensferry WwTW | 742 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331695 | 368236 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1SZ | CH51SZ | ch5 1sz | ch51sz | Flintshire | Sir Y Fflint | Queensferry WwTW | 545 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331919 | 368230 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1TA | CH51TA | ch5 1ta | ch51ta | Flintshire | Sir Y Fflint | Queensferry WwTW | 658 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331816 | 368181 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1TB | CH51TB | ch5 1tb | ch51tb | Flintshire | Sir Y Fflint | Queensferry WwTW | 617 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331883 | 368155 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1TD | CH51TD | ch5 1td | ch51td | Flintshire | Sir Y Fflint | Queensferry WwTW | 737 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331791 | 368078 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1TF | CH51TF | ch5 1tf | ch51tf | Flintshire | Sir Y Fflint | Queensferry WwTW | 841 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331664 | 368080 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1TG | CH51TG | ch5 1tg | ch51tg | Flintshire | Sir Y Fflint | Queensferry WwTW | 830 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331694 | 368053 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1TJ | CH51TJ | ch5 1tj | ch51tj | Flintshire | Sir Y Fflint | Queensferry WwTW | 1685 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330937 | 367651 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1TL | CH51TL | ch5 1tl | ch51tl | Flintshire | Sir Y Fflint | Queensferry WwTW | 1846 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330826 | 367525 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1TP | CH51TP | ch5 1tp | ch51tp | Flintshire | Sir Y Fflint | Queensferry WwTW | 939 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331542 | 368096 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1TQ | CH51TQ | ch5 1tq | ch51tq | Flintshire | Sir Y Fflint | Queensferry WwTW | 1322 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331197 | 367930 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1TR | CH51TR | ch5 1tr | ch51tr | Flintshire | Sir Y Fflint | Queensferry WwTW | 1241 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331203 | 368126 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1TW | CH51TW | ch5 1tw | ch51tw | Flintshire | Sir Y Fflint | Connahs Quay STW | 398 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330481 | 369063 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1UA | CH51UA | ch5 1ua | ch51ua | Flintshire | Sir Y Fflint | Connahs Quay STW | 1821 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330567 | 367589 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1UB | CH51UB | ch5 1ub | ch51ub | Flintshire | Sir Y Fflint | Connahs Quay STW | 1680 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330452 | 367714 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1UD | CH51UD | ch5 1ud | ch51ud | Flintshire | Sir Y Fflint | Connahs Quay STW | 1517 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330315 | 367865 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1UH | CH51UH | ch5 1uh | ch51uh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1985 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330453 | 367407 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1UJ | CH51UJ | ch5 1uj | ch51uj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1791 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330363 | 367594 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1UL | CH51UL | ch5 1ul | ch51ul | Flintshire | Sir Y Fflint | Connahs Quay STW | 1993 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330690 | 367439 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1UN | CH51UN | ch5 1un | ch51un | Flintshire | Sir Y Fflint | Connahs Quay STW | 2072 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330611 | 367342 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1UP | CH51UP | ch5 1up | ch51up | Flintshire | Sir Y Fflint | Connahs Quay STW | 2112 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330570 | 367295 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1UQ | CH51UQ | ch5 1uq | ch51uq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1976 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330598 | 367437 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1UR | CH51UR | ch5 1ur | ch51ur | Flintshire | Sir Y Fflint | Connahs Quay STW | 1938 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330720 | 367503 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1UW | CH51UW | ch5 1uw | ch51uw | Flintshire | Sir Y Fflint | Connahs Quay STW | 2089 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330450 | 367302 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XA | CH51XA | ch5 1xa | ch51xa | Flintshire | Sir Y Fflint | Connahs Quay STW | 1975 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330392 | 367412 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XB | CH51XB | ch5 1xb | ch51xb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1812 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330488 | 367586 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XD | CH51XD | ch5 1xd | ch51xd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1896 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330493 | 367502 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XE | CH51XE | ch5 1xe | ch51xe | Flintshire | Sir Y Fflint | Connahs Quay STW | 1571 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330320 | 367812 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XF | CH51XF | ch5 1xf | ch51xf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1752 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330294 | 367629 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XG | CH51XG | ch5 1xg | ch51xg | Flintshire | Sir Y Fflint | Connahs Quay STW | 1924 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330303 | 367458 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XH | CH51XH | ch5 1xh | ch51xh | Flintshire | Sir Y Fflint | Connahs Quay STW | 2167 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330385 | 367219 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XJ | CH51XJ | ch5 1xj | ch51xj | Flintshire | Sir Y Fflint | Connahs Quay STW | 2034 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330415 | 367354 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XL | CH51XL | ch5 1xl | ch51xl | Flintshire | Sir Y Fflint | Connahs Quay STW | 1506 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 330289 | 367875 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XP | CH51XP | ch5 1xp | ch51xp | Flintshire | Sir Y Fflint | Connahs Quay STW | 2219 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330518 | 367179 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XQ | CH51XQ | ch5 1xq | ch51xq | Flintshire | Sir Y Fflint | Connahs Quay STW | 2081 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330355 | 367303 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XR | CH51XR | ch5 1xr | ch51xr | Flintshire | Sir Y Fflint | Connahs Quay STW | 2158 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330473 | 367235 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XS | CH51XS | ch5 1xs | ch51xs | Flintshire | Sir Y Fflint | Connahs Quay STW | 1841 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330760 | 367615 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XT | CH51XT | ch5 1xt | ch51xt | Flintshire | Sir Y Fflint | Connahs Quay STW | 2204 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330396 | 367182 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XU | CH51XU | ch5 1xu | ch51xu | Flintshire | Sir Y Fflint | Queensferry WwTW | 1507 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331049 | 367815 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XX | CH51XX | ch5 1xx | ch51xx | Flintshire | Sir Y Fflint | Queensferry WwTW | 1749 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330850 | 367675 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XY | CH51XY | ch5 1xy | ch51xy | Flintshire | Sir Y Fflint | Queensferry WwTW | 1713 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330861 | 367729 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1XZ | CH51XZ | ch5 1xz | ch51xz | Flintshire | Sir Y Fflint | Queensferry WwTW | 1614 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330982 | 367715 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 1YA | CH51YA | ch5 1ya | ch51ya | Flintshire | Sir Y Fflint | Queensferry WwTW | 1614 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 330939 | 367795 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AA | CH52AA | ch5 2aa | ch52aa | Flintshire | Sir Y Fflint | Queensferry WwTW | 811 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332211 | 367729 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AB | CH52AB | ch5 2ab | ch52ab | Flintshire | Sir Y Fflint | Queensferry WwTW | 827 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332087 | 367749 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AD | CH52AD | ch5 2ad | ch52ad | Flintshire | Sir Y Fflint | Queensferry WwTW | 926 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332096 | 367641 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AE | CH52AE | ch5 2ae | ch52ae | Flintshire | Sir Y Fflint | Queensferry WwTW | 982 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332113 | 367577 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AF | CH52AF | ch5 2af | ch52af | Flintshire | Sir Y Fflint | Queensferry WwTW | 1582 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331834 | 367037 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AG | CH52AG | ch5 2ag | ch52ag | Flintshire | Sir Y Fflint | Queensferry WwTW | 841 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332183 | 367704 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AH | CH52AH | ch5 2ah | ch52ah | Flintshire | Sir Y Fflint | Queensferry WwTW | 1614 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331855 | 366996 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AJ | CH52AJ | ch5 2aj | ch52aj | Flintshire | Sir Y Fflint | Queensferry WwTW | 1296 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332052 | 367268 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AL | CH52AL | ch5 2al | ch52al | Flintshire | Sir Y Fflint | Queensferry WwTW | 1508 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333042 | 367168 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AN | CH52AN | ch5 2an | ch52an | Flintshire | Sir Y Fflint | Queensferry WwTW | 1360 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332083 | 367195 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AP | CH52AP | ch5 2ap | ch52ap | Flintshire | Sir Y Fflint | Queensferry WwTW | 1278 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332167 | 367262 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AQ | CH52AQ | ch5 2aq | ch52aq | Flintshire | Sir Y Fflint | Queensferry WwTW | 1408 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331417 | 367494 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AR | CH52AR | ch5 2ar | ch52ar | Flintshire | Sir Y Fflint | Queensferry WwTW | 1736 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331789 | 366890 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AS | CH52AS | ch5 2as | ch52as | Flintshire | Sir Y Fflint | Queensferry WwTW | 1484 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331926 | 367109 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AT | CH52AT | ch5 2at | ch52at | Flintshire | Sir Y Fflint | Queensferry WwTW | 1490 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332013 | 367078 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AU | CH52AU | ch5 2au | ch52au | Flintshire | Sir Y Fflint | Queensferry WwTW | 1594 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331917 | 366997 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AW | CH52AW | ch5 2aw | ch52aw | Flintshire | Sir Y Fflint | Queensferry WwTW | 1290 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332201 | 367245 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AX | CH52AX | ch5 2ax | ch52ax | Flintshire | Sir Y Fflint | Queensferry WwTW | 1619 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331966 | 366957 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AY | CH52AY | ch5 2ay | ch52ay | Flintshire | Sir Y Fflint | Queensferry WwTW | 1668 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331743 | 366981 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2AZ | CH52AZ | ch5 2az | ch52az | Flintshire | Sir Y Fflint | Queensferry WwTW | 1659 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331685 | 367016 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BA | CH52BA | ch5 2ba | ch52ba | Flintshire | Sir Y Fflint | Queensferry WwTW | 1746 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331645 | 366938 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BB | CH52BB | ch5 2bb | ch52bb | Flintshire | Sir Y Fflint | Queensferry WwTW | 1701 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331726 | 366952 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BD | CH52BD | ch5 2bd | ch52bd | Flintshire | Sir Y Fflint | Queensferry WwTW | 889 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332252 | 367642 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BE | CH52BE | ch5 2be | ch52be | Flintshire | Sir Y Fflint | Queensferry WwTW | 1790 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332003 | 366773 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BF | CH52BF | ch5 2bf | ch52bf | Flintshire | Sir Y Fflint | Queensferry WwTW | 1243 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332278 | 367284 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BG | CH52BG | ch5 2bg | ch52bg | Flintshire | Sir Y Fflint | Queensferry WwTW | 1810 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332133 | 366729 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BH | CH52BH | ch5 2bh | ch52bh | Flintshire | Sir Y Fflint | Queensferry WwTW | 2044 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331970 | 366520 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BJ | CH52BJ | ch5 2bj | ch52bj | Flintshire | Sir Y Fflint | Queensferry WwTW | 2074 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331960 | 366491 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BL | CH52BL | ch5 2bl | ch52bl | Flintshire | Sir Y Fflint | Queensferry WwTW | 1815 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332090 | 366731 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BN | CH52BN | ch5 2bn | ch52bn | Flintshire | Sir Y Fflint | Queensferry WwTW | 1888 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332131 | 366651 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BP | CH52BP | ch5 2bp | ch52bp | Flintshire | Sir Y Fflint | Queensferry WwTW | 1998 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332036 | 366554 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BQ | CH52BQ | ch5 2bq | ch52bq | Flintshire | Sir Y Fflint | Queensferry WwTW | 1953 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331994 | 366608 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BR | CH52BR | ch5 2br | ch52br | Flintshire | Sir Y Fflint | Queensferry WwTW | 1903 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331888 | 366684 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BS | CH52BS | ch5 2bs | ch52bs | Flintshire | Sir Y Fflint | Queensferry WwTW | 1880 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331972 | 366687 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BT | CH52BT | ch5 2bt | ch52bt | Flintshire | Sir Y Fflint | Queensferry WwTW | 1104 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 331492 | 367866 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BU | CH52BU | ch5 2bu | ch52bu | Flintshire | Sir Y Fflint | Queensferry WwTW | 1912 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332048 | 366640 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BW | CH52BW | ch5 2bw | ch52bw | Flintshire | Sir Y Fflint | Queensferry WwTW | 1988 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332097 | 366555 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BX | CH52BX | ch5 2bx | ch52bx | Flintshire | Sir Y Fflint | Queensferry WwTW | 2057 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331851 | 366535 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BY | CH52BY | ch5 2by | ch52by | Flintshire | Sir Y Fflint | Queensferry WwTW | 2093 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 332044 | 366457 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2BZ | CH52BZ | ch5 2bz | ch52bz | Flintshire | Sir Y Fflint | Queensferry WwTW | 1858 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332143 | 366680 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DA | CH52DA | ch5 2da | ch52da | Flintshire | Sir Y Fflint | Queensferry WwTW | 735 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332315 | 367790 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DD | CH52DD | ch5 2dd | ch52dd | Flintshire | Sir Y Fflint | Queensferry WwTW | 1147 | 720 | 700to900 | 1.44 | 1.05 | 0.77 | 13.41 | 7.15 | 7.91 | 333074 | 367610 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DH | CH52DH | ch5 2dh | ch52dh | Flintshire | Sir Y Fflint | Queensferry WwTW | 1004 | 720 | 700to900 | 1.44 | 1.05 | 0.77 | 13.41 | 7.15 | 7.91 | 332677 | 367564 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DJ | CH52DJ | ch5 2dj | ch52dj | Flintshire | Sir Y Fflint | Queensferry WwTW | 814 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332392 | 367708 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DL | CH52DL | ch5 2dl | ch52dl | Flintshire | Sir Y Fflint | Queensferry WwTW | 1356 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333063 | 367352 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DN | CH52DN | ch5 2dn | ch52dn | Flintshire | Sir Y Fflint | Queensferry WwTW | 981 | 720 | 700to900 | 1.44 | 1.05 | 0.77 | 13.41 | 7.15 | 7.91 | 332829 | 367651 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DP | CH52DP | ch5 2dp | ch52dp | Flintshire | Sir Y Fflint | Queensferry WwTW | 1110 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332674 | 367452 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DQ | CH52DQ | ch5 2dq | ch52dq | Flintshire | Sir Y Fflint | Queensferry WwTW | 859 | 720 | 700to900 | 1.44 | 1.05 | 0.77 | 13.41 | 7.15 | 7.91 | 332530 | 367677 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DR | CH52DR | ch5 2dr | ch52dr | Flintshire | Sir Y Fflint | Queensferry WwTW | 1148 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332676 | 367414 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DS | CH52DS | ch5 2ds | ch52ds | Flintshire | Sir Y Fflint | Queensferry WwTW | 832 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332311 | 367693 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DT | CH52DT | ch5 2dt | ch52dt | Flintshire | Sir Y Fflint | Queensferry WwTW | 1065 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332573 | 367475 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DU | CH52DU | ch5 2du | ch52du | Flintshire | Sir Y Fflint | Queensferry WwTW | 128 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332422 | 368402 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DW | CH52DW | ch5 2dw | ch52dw | Flintshire | Sir Y Fflint | Queensferry WwTW | 616 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332153 | 367949 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DX | CH52DX | ch5 2dx | ch52dx | Flintshire | Sir Y Fflint | Queensferry WwTW | 1364 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332312 | 367160 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DY | CH52DY | ch5 2dy | ch52dy | Flintshire | Sir Y Fflint | Queensferry WwTW | 1208 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332650 | 367345 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2DZ | CH52DZ | ch5 2dz | ch52dz | Flintshire | Sir Y Fflint | Queensferry WwTW | 1000 | 720 | 700to900 | 1.44 | 1.05 | 0.77 | 13.41 | 7.15 | 7.91 | 332513 | 367531 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EA | CH52EA | ch5 2ea | ch52ea | Flintshire | Sir Y Fflint | Queensferry WwTW | 1075 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332580 | 367466 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2ED | CH52ED | ch5 2ed | ch52ed | Flintshire | Sir Y Fflint | Queensferry WwTW | 1747 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332189 | 366786 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EE | CH52EE | ch5 2ee | ch52ee | Flintshire | Sir Y Fflint | Queensferry WwTW | 2061 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 332076 | 366484 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EF | CH52EF | ch5 2ef | ch52ef | Flintshire | Sir Y Fflint | Queensferry WwTW | 1438 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332261 | 367089 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EG | CH52EG | ch5 2eg | ch52eg | Flintshire | Sir Y Fflint | Queensferry WwTW | 1389 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332680 | 367167 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EH | CH52EH | ch5 2eh | ch52eh | Flintshire | Sir Y Fflint | Queensferry WwTW | 1244 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332449 | 367280 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EJ | CH52EJ | ch5 2ej | ch52ej | Flintshire | Sir Y Fflint | Queensferry WwTW | 1629 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332176 | 366906 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EL | CH52EL | ch5 2el | ch52el | Flintshire | Sir Y Fflint | Queensferry WwTW | 1476 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332148 | 367065 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EN | CH52EN | ch5 2en | ch52en | Flintshire | Sir Y Fflint | Queensferry WwTW | 1302 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332272 | 367225 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EP | CH52EP | ch5 2ep | ch52ep | Flintshire | Sir Y Fflint | Queensferry WwTW | 1309 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332367 | 367214 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EQ | CH52EQ | ch5 2eq | ch52eq | Flintshire | Sir Y Fflint | Queensferry WwTW | 1256 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332517 | 367274 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2ER | CH52ER | ch5 2er | ch52er | Flintshire | Sir Y Fflint | Queensferry WwTW | 1581 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332114 | 366964 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2ES | CH52ES | ch5 2es | ch52es | Flintshire | Sir Y Fflint | Queensferry WwTW | 1628 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332119 | 366915 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2ET | CH52ET | ch5 2et | ch52et | Flintshire | Sir Y Fflint | Queensferry WwTW | 1647 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332138 | 366893 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EU | CH52EU | ch5 2eu | ch52eu | Flintshire | Sir Y Fflint | Queensferry WwTW | 1625 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332079 | 366926 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EW | CH52EW | ch5 2ew | ch52ew | Flintshire | Sir Y Fflint | Queensferry WwTW | 1535 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332065 | 367020 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EX | CH52EX | ch5 2ex | ch52ex | Flintshire | Sir Y Fflint | Queensferry WwTW | 1164 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332409 | 367359 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EY | CH52EY | ch5 2ey | ch52ey | Flintshire | Sir Y Fflint | Queensferry WwTW | 1194 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332348 | 367329 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2EZ | CH52EZ | ch5 2ez | ch52ez | Flintshire | Sir Y Fflint | Queensferry WwTW | 1848 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331988 | 366716 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FA | CH52FA | ch5 2fa | ch52fa | Flintshire | Sir Y Fflint | Queensferry WwTW | 1012 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331675 | 367795 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FB | CH52FB | ch5 2fb | ch52fb | Flintshire | Sir Y Fflint | Queensferry WwTW | 925 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331809 | 367794 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FD | CH52FD | ch5 2fd | ch52fd | Flintshire | Sir Y Fflint | Queensferry WwTW | 960 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331753 | 367794 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FE | CH52FE | ch5 2fe | ch52fe | Flintshire | Sir Y Fflint | Queensferry WwTW | 909 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331792 | 367829 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FF | CH52FF | ch5 2ff | ch52ff | Flintshire | Sir Y Fflint | Queensferry WwTW | 1018 | 720 | 700to900 | 1.44 | 1.05 | 0.77 | 13.41 | 7.15 | 7.91 | 332921 | 367661 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FG | CH52FG | ch5 2fg | ch52fg | Flintshire | Sir Y Fflint | Queensferry WwTW | 2171 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 333967 | 367043 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FH | CH52FH | ch5 2fh | ch52fh | Flintshire | Sir Y Fflint | Queensferry WwTW | 1021 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332893 | 369404 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FJ | CH52FJ | ch5 2fj | ch52fj | Flintshire | Sir Y Fflint | Queensferry WwTW | 1029 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332787 | 369466 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FL | CH52FL | ch5 2fl | ch52fl | Flintshire | Sir Y Fflint | Queensferry WwTW | 1279 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 332919 | 369681 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FN | CH52FN | ch5 2fn | ch52fn | Flintshire | Sir Y Fflint | Queensferry WwTW | 1242 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 333033 | 369577 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FP | CH52FP | ch5 2fp | ch52fp | Flintshire | Sir Y Fflint | Queensferry WwTW | 1251 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 333001 | 369607 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FQ | CH52FQ | ch5 2fq | ch52fq | Flintshire | Sir Y Fflint | Queensferry WwTW | 1173 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 332948 | 369547 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FR | CH52FR | ch5 2fr | ch52fr | Flintshire | Sir Y Fflint | Queensferry WwTW | 1313 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 332936 | 369710 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FS | CH52FS | ch5 2fs | ch52fs | Flintshire | Sir Y Fflint | Queensferry WwTW | 1170 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 333015 | 369503 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FT | CH52FT | ch5 2ft | ch52ft | Flintshire | Sir Y Fflint | Queensferry WwTW | 1141 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333003 | 369477 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FW | CH52FW | ch5 2fw | ch52fw | Flintshire | Sir Y Fflint | Queensferry WwTW | 943 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332849 | 369339 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FX | CH52FX | ch5 2fx | ch52fx | Flintshire | Sir Y Fflint | Queensferry WwTW | 1014 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332839 | 369425 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FY | CH52FY | ch5 2fy | ch52fy | Flintshire | Sir Y Fflint | Queensferry WwTW | 997 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332958 | 369333 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2FZ | CH52FZ | ch5 2fz | ch52fz | Flintshire | Sir Y Fflint | Queensferry WwTW | 1347 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 332986 | 369724 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2GB | CH52GB | ch5 2gb | ch52gb | Flintshire | Sir Y Fflint | Queensferry WwTW | 1201 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 332403 | 367322 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2GE | CH52GE | ch5 2ge | ch52ge | Flintshire | Sir Y Fflint | Queensferry WwTW | 270 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332438 | 368785 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2GF | CH52GF | ch5 2gf | ch52gf | Flintshire | Sir Y Fflint | Queensferry WwTW | 721 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332890 | 369031 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2GG | CH52GG | ch5 2gg | ch52gg | Flintshire | Sir Y Fflint | Queensferry WwTW | 317 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332068 | 368581 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2GH | CH52GH | ch5 2gh | ch52gh | Flintshire | Sir Y Fflint | Queensferry WwTW | 1182 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 332613 | 369680 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2GJ | CH52GJ | ch5 2gj | ch52gj | Flintshire | Sir Y Fflint | Queensferry WwTW | 1249 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 332620 | 369747 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2GL | CH52GL | ch5 2gl | ch52gl | Flintshire | Sir Y Fflint | Queensferry WwTW | 1211 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 332583 | 369715 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2GP | CH52GP | ch5 2gp | ch52gp | Flintshire | Sir Y Fflint | Queensferry WwTW | 1182 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 332636 | 369675 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2HH | CH52HH | ch5 2hh | ch52hh | Flintshire | Sir Y Fflint | Queensferry WwTW | 485 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332546 | 368977 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2HJ | CH52HJ | ch5 2hj | ch52hj | Flintshire | Sir Y Fflint | Queensferry WwTW | 565 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332408 | 369086 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2HL | CH52HL | ch5 2hl | ch52hl | Flintshire | Sir Y Fflint | Queensferry WwTW | 630 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332653 | 369089 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2HN | CH52HN | ch5 2hn | ch52hn | Flintshire | Sir Y Fflint | Queensferry WwTW | 821 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332581 | 369317 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2HP | CH52HP | ch5 2hp | ch52hp | Flintshire | Sir Y Fflint | Queensferry WwTW | 687 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332574 | 369181 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2HR | CH52HR | ch5 2hr | ch52hr | Flintshire | Sir Y Fflint | Queensferry WwTW | 1313 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 333249 | 369505 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2HT | CH52HT | ch5 2ht | ch52ht | Flintshire | Sir Y Fflint | Queensferry WwTW | 533 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332642 | 368985 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2HU | CH52HU | ch5 2hu | ch52hu | Flintshire | Sir Y Fflint | Queensferry WwTW | 655 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332765 | 369051 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2HW | CH52HW | ch5 2hw | ch52hw | Flintshire | Sir Y Fflint | Queensferry WwTW | 1001 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332681 | 369476 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2HX | CH52HX | ch5 2hx | ch52hx | Flintshire | Sir Y Fflint | Queensferry WwTW | 798 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332931 | 369098 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2HY | CH52HY | ch5 2hy | ch52hy | Flintshire | Sir Y Fflint | Queensferry WwTW | 572 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332587 | 369055 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2HZ | CH52HZ | ch5 2hz | ch52hz | Flintshire | Sir Y Fflint | Queensferry WwTW | 630 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332513 | 369137 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JA | CH52JA | ch5 2ja | ch52ja | Flintshire | Sir Y Fflint | Queensferry WwTW | 657 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332548 | 369157 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JB | CH52JB | ch5 2jb | ch52jb | Flintshire | Sir Y Fflint | Queensferry WwTW | 694 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332435 | 369213 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JD | CH52JD | ch5 2jd | ch52jd | Flintshire | Sir Y Fflint | Queensferry WwTW | 671 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332453 | 369189 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JE | CH52JE | ch5 2je | ch52je | Flintshire | Sir Y Fflint | Queensferry WwTW | 856 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332602 | 369348 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JF | CH52JF | ch5 2jf | ch52jf | Flintshire | Sir Y Fflint | Queensferry WwTW | 880 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332748 | 369321 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JG | CH52JG | ch5 2jg | ch52jg | Flintshire | Sir Y Fflint | Queensferry WwTW | 852 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332697 | 369312 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JH | CH52JH | ch5 2jh | ch52jh | Flintshire | Sir Y Fflint | Queensferry WwTW | 732 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332782 | 369133 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JJ | CH52JJ | ch5 2jj | ch52jj | Flintshire | Sir Y Fflint | Queensferry WwTW | 890 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332857 | 369272 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JL | CH52JL | ch5 2jl | ch52jl | Flintshire | Sir Y Fflint | Queensferry WwTW | 786 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332686 | 369245 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JN | CH52JN | ch5 2jn | ch52jn | Flintshire | Sir Y Fflint | Queensferry WwTW | 791 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332736 | 369227 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JP | CH52JP | ch5 2jp | ch52jp | Flintshire | Sir Y Fflint | Queensferry WwTW | 763 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332844 | 369126 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JQ | CH52JQ | ch5 2jq | ch52jq | Flintshire | Sir Y Fflint | Queensferry WwTW | 775 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332797 | 369174 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JR | CH52JR | ch5 2jr | ch52jr | Flintshire | Sir Y Fflint | Queensferry WwTW | 630 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332836 | 368955 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JS | CH52JS | ch5 2js | ch52js | Flintshire | Sir Y Fflint | Queensferry WwTW | 556 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332801 | 368883 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JT | CH52JT | ch5 2jt | ch52jt | Flintshire | Sir Y Fflint | Queensferry WwTW | 796 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332984 | 369039 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JU | CH52JU | ch5 2ju | ch52ju | Flintshire | Sir Y Fflint | Queensferry WwTW | 892 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333062 | 369095 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JW | CH52JW | ch5 2jw | ch52jw | Flintshire | Sir Y Fflint | Queensferry WwTW | 731 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332726 | 369165 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JX | CH52JX | ch5 2jx | ch52jx | Flintshire | Sir Y Fflint | Queensferry WwTW | 671 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332739 | 369088 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JY | CH52JY | ch5 2jy | ch52jy | Flintshire | Sir Y Fflint | Queensferry WwTW | 2211 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 333933 | 370094 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2JZ | CH52JZ | ch5 2jz | ch52jz | Flintshire | Sir Y Fflint | Queensferry WwTW | 2121 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 333469 | 370341 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LA | CH52LA | ch5 2la | ch52la | Flintshire | Sir Y Fflint | Queensferry WwTW | 1823 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 332732 | 370310 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LB | CH52LB | ch5 2lb | ch52lb | Flintshire | Sir Y Fflint | Queensferry WwTW | 2029 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 332383 | 370550 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LD | CH52LD | ch5 2ld | ch52ld | Flintshire | Sir Y Fflint | Queensferry WwTW | 1958 | 719 | 700to900 | 1.44 | 1.05 | 0.77 | 13.39 | 7.14 | 7.9 | 332405 | 370479 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LE | CH52LE | ch5 2le | ch52le | Flintshire | Sir Y Fflint | Queensferry WwTW | 1932 | 719 | 700to900 | 1.44 | 1.05 | 0.77 | 13.39 | 7.14 | 7.9 | 332479 | 370451 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LF | CH52LF | ch5 2lf | ch52lf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1826 | 719 | 700to900 | 1.44 | 1.05 | 0.77 | 13.39 | 7.14 | 7.9 | 331063 | 371009 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LH | CH52LH | ch5 2lh | ch52lh | Flintshire | Sir Y Fflint | Queensferry WwTW | 2360 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334380 | 369771 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LJ | CH52LJ | ch5 2lj | ch52lj | Flintshire | Sir Y Fflint | Queensferry WwTW | 2677 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 333620 | 370893 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LL | CH52LL | ch5 2ll | ch52ll | Flintshire | Sir Y Fflint | Connahs Quay STW | 2558 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 331286 | 371713 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LQ | CH52LQ | ch5 2lq | ch52lq | Flintshire | Sir Y Fflint | Queensferry WwTW | 2236 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 334568 | 368973 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LR | CH52LR | ch5 2lr | ch52lr | Flintshire | Sir Y Fflint | Queensferry WwTW | 1935 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 333361 | 370188 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LS | CH52LS | ch5 2ls | ch52ls | Flintshire | Sir Y Fflint | Queensferry WwTW | 1941 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 333523 | 370089 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LT | CH52LT | ch5 2lt | ch52lt | Flintshire | Sir Y Fflint | Queensferry WwTW | 1684 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 333409 | 369853 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LW | CH52LW | ch5 2lw | ch52lw | Flintshire | Sir Y Fflint | Connahs Quay STW | 2308 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 330528 | 371669 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2LY | CH52LY | ch5 2ly | ch52ly | Flintshire | Sir Y Fflint | Queensferry WwTW | 1659 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 333429 | 369806 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NA | CH52NA | ch5 2na | ch52na | Flintshire | Sir Y Fflint | Queensferry WwTW | 2384 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334030 | 370240 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NB | CH52NB | ch5 2nb | ch52nb | Flintshire | Sir Y Fflint | Queensferry WwTW | 2351 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334113 | 370109 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2ND | CH52ND | ch5 2nd | ch52nd | Flintshire | Sir Y Fflint | Queensferry WwTW | 2366 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334157 | 370082 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NE | CH52NE | ch5 2ne | ch52ne | Flintshire | Sir Y Fflint | Queensferry WwTW | 2342 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334194 | 370001 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NG | CH52NG | ch5 2ng | ch52ng | Flintshire | Sir Y Fflint | Queensferry WwTW | 2227 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 334062 | 369979 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NH | CH52NH | ch5 2nh | ch52nh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1324 | 718 | 700to900 | 1.44 | 1.05 | 0.77 | 13.37 | 7.13 | 7.88 | 329785 | 370623 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NL | CH52NL | ch5 2nl | ch52nl | Flintshire | Sir Y Fflint | Queensferry WwTW | 1964 | 719 | 700to900 | 1.44 | 1.05 | 0.77 | 13.39 | 7.14 | 7.9 | 332046 | 370457 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NN | CH52NN | ch5 2nn | ch52nn | Flintshire | Sir Y Fflint | Queensferry WwTW | 2565 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 332888 | 371035 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NQ | CH52NQ | ch5 2nq | ch52nq | Flintshire | Sir Y Fflint | Queensferry WwTW | 2101 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 333929 | 369939 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NR | CH52NR | ch5 2nr | ch52nr | Flintshire | Sir Y Fflint | Queensferry WwTW | 2288 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 332377 | 370809 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NS | CH52NS | ch5 2ns | ch52ns | Flintshire | Sir Y Fflint | Queensferry WwTW | 2090 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 332536 | 370605 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NT | CH52NT | ch5 2nt | ch52nt | Flintshire | Sir Y Fflint | Queensferry WwTW | 2238 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 332850 | 370709 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NU | CH52NU | ch5 2nu | ch52nu | Flintshire | Sir Y Fflint | Queensferry WwTW | 2335 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 333224 | 370698 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NW | CH52NW | ch5 2nw | ch52nw | Flintshire | Sir Y Fflint | Queensferry WwTW | 2741 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 332653 | 371248 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NX | CH52NX | ch5 2nx | ch52nx | Flintshire | Sir Y Fflint | Queensferry WwTW | 2506 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 332660 | 371011 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2NY | CH52NY | ch5 2ny | ch52ny | Flintshire | Sir Y Fflint | Queensferry WwTW | 2259 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 333511 | 370476 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PA | CH52PA | ch5 2pa | ch52pa | Flintshire | Sir Y Fflint | Queensferry WwTW | 1533 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333165 | 367206 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PB | CH52PB | ch5 2pb | ch52pb | Flintshire | Sir Y Fflint | Queensferry WwTW | 1572 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333152 | 367154 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PD | CH52PD | ch5 2pd | ch52pd | Flintshire | Sir Y Fflint | Queensferry WwTW | 1695 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333265 | 367078 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PE | CH52PE | ch5 2pe | ch52pe | Flintshire | Sir Y Fflint | Queensferry WwTW | 1724 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333290 | 367059 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PF | CH52PF | ch5 2pf | ch52pf | Flintshire | Sir Y Fflint | Queensferry WwTW | 1626 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333131 | 367081 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PG | CH52PG | ch5 2pg | ch52pg | Flintshire | Sir Y Fflint | Queensferry WwTW | 1623 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333228 | 367139 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PH | CH52PH | ch5 2ph | ch52ph | Flintshire | Sir Y Fflint | Queensferry WwTW | 1684 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333351 | 367148 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PJ | CH52PJ | ch5 2pj | ch52pj | Flintshire | Sir Y Fflint | Queensferry WwTW | 1738 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333171 | 366976 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PL | CH52PL | ch5 2pl | ch52pl | Flintshire | Sir Y Fflint | Queensferry WwTW | 1800 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333236 | 366940 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PN | CH52PN | ch5 2pn | ch52pn | Flintshire | Sir Y Fflint | Queensferry WwTW | 1788 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333265 | 366970 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PP | CH52PP | ch5 2pp | ch52pp | Flintshire | Sir Y Fflint | Queensferry WwTW | 1812 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333384 | 367015 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PQ | CH52PQ | ch5 2pq | ch52pq | Flintshire | Sir Y Fflint | Queensferry WwTW | 1612 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333259 | 367172 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PR | CH52PR | ch5 2pr | ch52pr | Flintshire | Sir Y Fflint | Queensferry WwTW | 1810 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333409 | 367034 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PS | CH52PS | ch5 2ps | ch52ps | Flintshire | Sir Y Fflint | Queensferry WwTW | 1848 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333283 | 366911 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PT | CH52PT | ch5 2pt | ch52pt | Flintshire | Sir Y Fflint | Queensferry WwTW | 1830 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 333512 | 367086 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PU | CH52PU | ch5 2pu | ch52pu | Flintshire | Sir Y Fflint | Queensferry WwTW | 1685 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333323 | 367127 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PW | CH52PW | ch5 2pw | ch52pw | Flintshire | Sir Y Fflint | Queensferry WwTW | 1656 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 333725 | 367559 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2PZ | CH52PZ | ch5 2pz | ch52pz | Flintshire | Sir Y Fflint | Queensferry WwTW | 1927 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333354 | 366861 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QA | CH52QA | ch5 2qa | ch52qa | Flintshire | Sir Y Fflint | Queensferry WwTW | 1520 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333006 | 367138 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QB | CH52QB | ch5 2qb | ch52qb | Flintshire | Sir Y Fflint | Queensferry WwTW | 1624 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 333610 | 367464 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QD | CH52QD | ch5 2qd | ch52qd | Flintshire | Sir Y Fflint | Queensferry WwTW | 1468 | 720 | 700to900 | 1.44 | 1.05 | 0.77 | 13.41 | 7.15 | 7.91 | 333499 | 367574 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QE | CH52QE | ch5 2qe | ch52qe | Flintshire | Sir Y Fflint | Queensferry WwTW | 1484 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333337 | 367389 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QF | CH52QF | ch5 2qf | ch52qf | Flintshire | Sir Y Fflint | Queensferry WwTW | 1740 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 333544 | 367231 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QG | CH52QG | ch5 2qg | ch52qg | Flintshire | Sir Y Fflint | Queensferry WwTW | 1771 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 333629 | 367268 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QH | CH52QH | ch5 2qh | ch52qh | Flintshire | Sir Y Fflint | Queensferry WwTW | 1845 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 333680 | 367214 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QJ | CH52QJ | ch5 2qj | ch52qj | Flintshire | Sir Y Fflint | Queensferry WwTW | 909 | 720 | 700to900 | 1.44 | 1.05 | 0.77 | 13.41 | 7.15 | 7.91 | 332895 | 367774 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QL | CH52QL | ch5 2ql | ch52ql | Flintshire | Sir Y Fflint | Queensferry WwTW | 2051 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333307 | 366694 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QN | CH52QN | ch5 2qn | ch52qn | Flintshire | Sir Y Fflint | Queensferry WwTW | 1763 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333142 | 366933 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QP | CH52QP | ch5 2qp | ch52qp | Flintshire | Sir Y Fflint | Queensferry WwTW | 1398 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333082 | 367314 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QQ | CH52QQ | ch5 2qq | ch52qq | Flintshire | Sir Y Fflint | Queensferry WwTW | 1550 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 333651 | 367638 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QS | CH52QS | ch5 2qs | ch52qs | Flintshire | Sir Y Fflint | Queensferry WwTW | 1702 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 333541 | 367279 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QT | CH52QT | ch5 2qt | ch52qt | Flintshire | Sir Y Fflint | Queensferry WwTW | 2795 | 703 | 700to900 | 1.4 | 1.03 | 0.75 | 13.09 | 6.98 | 7.72 | 335146 | 368909 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QU | CH52QU | ch5 2qu | ch52qu | Flintshire | Sir Y Fflint | Queensferry WwTW | 1794 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 333587 | 367196 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QW | CH52QW | ch5 2qw | ch52qw | Flintshire | Sir Y Fflint | Queensferry WwTW | 1609 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332949 | 367018 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QX | CH52QX | ch5 2qx | ch52qx | Flintshire | Sir Y Fflint | Queensferry WwTW | 1556 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333481 | 367424 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2QZ | CH52QZ | ch5 2qz | ch52qz | Flintshire | Sir Y Fflint | Queensferry WwTW | 2073 | 714 | 700to900 | 1.43 | 1.04 | 0.77 | 13.3 | 7.09 | 7.84 | 333920 | 367136 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2RA | CH52RA | ch5 2ra | ch52ra | Flintshire | Sir Y Fflint | Queensferry WwTW | 372 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332518 | 368867 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2RB | CH52RB | ch5 2rb | ch52rb | Flintshire | Sir Y Fflint | Queensferry WwTW | 1044 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333096 | 369281 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2RD | CH52RD | ch5 2rd | ch52rd | Flintshire | Sir Y Fflint | Queensferry WwTW | 326 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332336 | 368845 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2RE | CH52RE | ch5 2re | ch52re | Flintshire | Sir Y Fflint | Queensferry WwTW | 630 | 720 | 700to900 | 1.44 | 1.05 | 0.77 | 13.41 | 7.15 | 7.91 | 332611 | 367936 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2RF | CH52RF | ch5 2rf | ch52rf | Flintshire | Sir Y Fflint | Queensferry WwTW | 1160 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333140 | 369397 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2RG | CH52RG | ch5 2rg | ch52rg | Flintshire | Sir Y Fflint | Queensferry WwTW | 1079 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333084 | 369339 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2RH | CH52RH | ch5 2rh | ch52rh | Flintshire | Sir Y Fflint | Queensferry WwTW | 1247 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333408 | 369225 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2RJ | CH52RJ | ch5 2rj | ch52rj | Flintshire | Sir Y Fflint | Queensferry WwTW | 1264 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333487 | 369129 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2RL | CH52RL | ch5 2rl | ch52rl | Flintshire | Sir Y Fflint | Queensferry WwTW | 1259 | 708 | 700to900 | 1.42 | 1.04 | 0.76 | 13.18 | 7.03 | 7.77 | 333534 | 369021 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2RN | CH52RN | ch5 2rn | ch52rn | Flintshire | Sir Y Fflint | Queensferry WwTW | 691 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332958 | 368899 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2RQ | CH52RQ | ch5 2rq | ch52rq | Flintshire | Sir Y Fflint | Queensferry WwTW | 1153 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333082 | 369435 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2RW | CH52RW | ch5 2rw | ch52rw | Flintshire | Sir Y Fflint | Queensferry WwTW | 254 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332381 | 368776 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SA | CH52SA | ch5 2sa | ch52sa | Flintshire | Sir Y Fflint | Queensferry WwTW | 1361 | 708 | 700to900 | 1.42 | 1.04 | 0.76 | 13.18 | 7.03 | 7.77 | 333660 | 368981 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SB | CH52SB | ch5 2sb | ch52sb | Flintshire | Sir Y Fflint | Queensferry WwTW | 1304 | 708 | 700to900 | 1.42 | 1.04 | 0.76 | 13.18 | 7.03 | 7.77 | 333631 | 368884 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SD | CH52SD | ch5 2sd | ch52sd | Flintshire | Sir Y Fflint | Queensferry WwTW | 990 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333349 | 368720 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SE | CH52SE | ch5 2se | ch52se | Flintshire | Sir Y Fflint | Queensferry WwTW | 1043 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333412 | 368662 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SF | CH52SF | ch5 2sf | ch52sf | Flintshire | Sir Y Fflint | Queensferry WwTW | 927 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333297 | 368647 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SG | CH52SG | ch5 2sg | ch52sg | Flintshire | Sir Y Fflint | Queensferry WwTW | 1022 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333397 | 368608 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SH | CH52SH | ch5 2sh | ch52sh | Flintshire | Sir Y Fflint | Queensferry WwTW | 477 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332679 | 368892 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SJ | CH52SJ | ch5 2sj | ch52sj | Flintshire | Sir Y Fflint | Queensferry WwTW | 1134 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333498 | 368703 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SL | CH52SL | ch5 2sl | ch52sl | Flintshire | Sir Y Fflint | Queensferry WwTW | 429 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332647 | 368857 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SN | CH52SN | ch5 2sn | ch52sn | Flintshire | Sir Y Fflint | Queensferry WwTW | 246 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332496 | 368738 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SP | CH52SP | ch5 2sp | ch52sp | Flintshire | Sir Y Fflint | Queensferry WwTW | 400 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332604 | 368852 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SQ | CH52SQ | ch5 2sq | ch52sq | Flintshire | Sir Y Fflint | Queensferry WwTW | 1129 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 333487 | 368739 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SR | CH52SR | ch5 2sr | ch52sr | Flintshire | Sir Y Fflint | Queensferry WwTW | 342 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332546 | 368820 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SS | CH52SS | ch5 2ss | ch52ss | Flintshire | Sir Y Fflint | Queensferry WwTW | 290 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332494 | 368788 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2ST | CH52ST | ch5 2st | ch52st | Flintshire | Sir Y Fflint | Queensferry WwTW | 526 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 332721 | 368921 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2SW | CH52SW | ch5 2sw | ch52sw | Flintshire | Sir Y Fflint | Queensferry WwTW | 242 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332434 | 368758 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2TA | CH52TA | ch5 2ta | ch52ta | Flintshire | Sir Y Fflint | Queensferry WwTW | 261 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 332145 | 368638 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2TB | CH52TB | ch5 2tb | ch52tb | Flintshire | Sir Y Fflint | Queensferry WwTW | 433 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331953 | 368445 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2TE | CH52TE | ch5 2te | ch52te | Flintshire | Sir Y Fflint | Queensferry WwTW | 239 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332143 | 368482 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2TF | CH52TF | ch5 2tf | ch52tf | Flintshire | Sir Y Fflint | Queensferry WwTW | 357 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332054 | 368374 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2TT | CH52TT | ch5 2tt | ch52tt | Flintshire | Sir Y Fflint | Queensferry WwTW | 1294 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331677 | 367435 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2TW | CH52TW | ch5 2tw | ch52tw | Flintshire | Sir Y Fflint | Connahs Quay STW | 2193 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 331588 | 371109 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2TX | CH52TX | ch5 2tx | ch52tx | Flintshire | Sir Y Fflint | Queensferry WwTW | 1063 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331711 | 367695 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2TY | CH52TY | ch5 2ty | ch52ty | Flintshire | Sir Y Fflint | Queensferry WwTW | 1201 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331646 | 367571 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2TZ | CH52TZ | ch5 2tz | ch52tz | Flintshire | Sir Y Fflint | Queensferry WwTW | 1211 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 331689 | 367527 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2UA | CH52UA | ch5 2ua | ch52ua | Flintshire | Sir Y Fflint | Connahs Quay STW | 2696 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 331947 | 371465 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2UL | CH52UL | ch5 2ul | ch52ul | Flintshire | Sir Y Fflint | Connahs Quay STW | 1813 | 718 | 700to900 | 1.44 | 1.05 | 0.77 | 13.37 | 7.13 | 7.88 | 329819 | 371143 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2UW | CH52UW | ch5 2uw | ch52uw | Flintshire | Sir Y Fflint | Queensferry WwTW | 1709 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333411 | 367161 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 2ZA | CH52ZA | ch5 2za | ch52za | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AA | CH53AA | ch5 3aa | ch53aa | Flintshire | Sir Y Fflint | Queensferry WwTW | 2308 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330612 | 367039 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AB | CH53AB | ch5 3ab | ch53ab | Flintshire | Sir Y Fflint | Queensferry WwTW | 2353 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330551 | 367042 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AE | CH53AE | ch5 3ae | ch53ae | Flintshire | Sir Y Fflint | Connahs Quay STW | 2142 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330635 | 367275 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AF | CH53AF | ch5 3af | ch53af | Flintshire | Sir Y Fflint | Connahs Quay STW | 2153 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330631 | 367264 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AG | CH53AG | ch5 3ag | ch53ag | Flintshire | Sir Y Fflint | Connahs Quay STW | 2258 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330453 | 367133 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AH | CH53AH | ch5 3ah | ch53ah | Flintshire | Sir Y Fflint | Connahs Quay STW | 2297 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330239 | 367084 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AJ | CH53AJ | ch5 3aj | ch53aj | Flintshire | Sir Y Fflint | Connahs Quay STW | 2181 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330159 | 367201 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AL | CH53AL | ch5 3al | ch53al | Flintshire | Sir Y Fflint | Connahs Quay STW | 2486 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329878 | 366921 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AN | CH53AN | ch5 3an | ch53an | Flintshire | Sir Y Fflint | Connahs Quay STW | 2561 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329840 | 366851 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AP | CH53AP | ch5 3ap | ch53ap | Flintshire | Sir Y Fflint | Connahs Quay STW | 2712 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329817 | 366702 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AQ | CH53AQ | ch5 3aq | ch53aq | Flintshire | Sir Y Fflint | Connahs Quay STW | 3067 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329352 | 366445 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AR | CH53AR | ch5 3ar | ch53ar | Flintshire | Sir Y Fflint | Connahs Quay STW | 2681 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329753 | 366745 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AS | CH53AS | ch5 3as | ch53as | Flintshire | Sir Y Fflint | Connahs Quay STW | 2632 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329716 | 366802 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AT | CH53AT | ch5 3at | ch53at | Flintshire | Sir Y Fflint | Connahs Quay STW | 2698 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329635 | 366752 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AU | CH53AU | ch5 3au | ch53au | Flintshire | Sir Y Fflint | Connahs Quay STW | 2907 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329421 | 366592 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AW | CH53AW | ch5 3aw | ch53aw | Flintshire | Sir Y Fflint | Connahs Quay STW | 2632 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329806 | 366785 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AX | CH53AX | ch5 3ax | ch53ax | Flintshire | Sir Y Fflint | Connahs Quay STW | 2881 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329512 | 366594 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AY | CH53AY | ch5 3ay | ch53ay | Flintshire | Sir Y Fflint | Connahs Quay STW | 3141 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329210 | 366414 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3AZ | CH53AZ | ch5 3az | ch53az | Flintshire | Sir Y Fflint | Connahs Quay STW | 3204 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329009 | 366423 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BA | CH53BA | ch5 3ba | ch53ba | Flintshire | Sir Y Fflint | Connahs Quay STW | 2087 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330662 | 367337 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BB | CH53BB | ch5 3bb | ch53bb | Flintshire | Sir Y Fflint | Connahs Quay STW | 3235 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 328959 | 366411 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BD | CH53BD | ch5 3bd | ch53bd | Flintshire | Sir Y Fflint | Connahs Quay STW | 3417 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 328586 | 366391 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BE | CH53BE | ch5 3be | ch53be | Flintshire | Sir Y Fflint | Connahs Quay STW | 3513 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 328482 | 366340 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BF | CH53BF | ch5 3bf | ch53bf | Flintshire | Sir Y Fflint | Connahs Quay STW | 2370 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330050 | 367018 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BG | CH53BG | ch5 3bg | ch53bg | Flintshire | Sir Y Fflint | Connahs Quay STW | 3765 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 328052 | 366318 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BH | CH53BH | ch5 3bh | ch53bh | Flintshire | Sir Y Fflint | Connahs Quay STW | 2922 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329317 | 366609 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BJ | CH53BJ | ch5 3bj | ch53bj | Flintshire | Sir Y Fflint | Connahs Quay STW | 2879 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329269 | 366671 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BL | CH53BL | ch5 3bl | ch53bl | Flintshire | Sir Y Fflint | Connahs Quay STW | 2965 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329280 | 366576 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BN | CH53BN | ch5 3bn | ch53bn | Flintshire | Sir Y Fflint | Connahs Quay STW | 3044 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329386 | 366459 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BP | CH53BP | ch5 3bp | ch53bp | Flintshire | Sir Y Fflint | Connahs Quay STW | 3038 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 328927 | 366642 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BQ | CH53BQ | ch5 3bq | ch53bq | Flintshire | Sir Y Fflint | Connahs Quay STW | 3923 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 327799 | 366310 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BR | CH53BR | ch5 3br | ch53br | Flintshire | Sir Y Fflint | Connahs Quay STW | 3021 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329029 | 366613 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BS | CH53BS | ch5 3bs | ch53bs | Flintshire | Sir Y Fflint | Connahs Quay STW | 2678 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329548 | 366794 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BT | CH53BT | ch5 3bt | ch53bt | Flintshire | Sir Y Fflint | Connahs Quay STW | 2725 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329458 | 366771 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BU | CH53BU | ch5 3bu | ch53bu | Flintshire | Sir Y Fflint | Connahs Quay STW | 2596 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329622 | 366860 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BW | CH53BW | ch5 3bw | ch53bw | Flintshire | Sir Y Fflint | Connahs Quay STW | 3778 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 328235 | 366180 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BX | CH53BX | ch5 3bx | ch53bx | Flintshire | Sir Y Fflint | Connahs Quay STW | 2678 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329463 | 366818 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BY | CH53BY | ch5 3by | ch53by | Flintshire | Sir Y Fflint | Connahs Quay STW | 2579 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329358 | 366957 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3BZ | CH53BZ | ch5 3bz | ch53bz | Flintshire | Sir Y Fflint | Connahs Quay STW | 2599 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 328843 | 367189 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DA | CH53DA | ch5 3da | ch53da | Flintshire | Sir Y Fflint | Connahs Quay STW | 2744 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329336 | 366790 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DB | CH53DB | ch5 3db | ch53db | Flintshire | Sir Y Fflint | Connahs Quay STW | 2880 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329367 | 366636 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DD | CH53DD | ch5 3dd | ch53dd | Flintshire | Sir Y Fflint | Queensferry WwTW | 2762 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 330977 | 366143 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DF | CH53DF | ch5 3df | ch53df | Flintshire | Sir Y Fflint | Queensferry WwTW | 2761 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331461 | 365919 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DG | CH53DG | ch5 3dg | ch53dg | Flintshire | Sir Y Fflint | Queensferry WwTW | 2849 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331323 | 365877 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DH | CH53DH | ch5 3dh | ch53dh | Flintshire | Sir Y Fflint | Queensferry WwTW | 2891 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331335 | 365827 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DJ | CH53DJ | ch5 3dj | ch53dj | Flintshire | Sir Y Fflint | Queensferry WwTW | 2933 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 330880 | 366002 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DL | CH53DL | ch5 3dl | ch53dl | Flintshire | Sir Y Fflint | Queensferry WwTW | 2881 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 330994 | 365997 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DN | CH53DN | ch5 3dn | ch53dn | Flintshire | Sir Y Fflint | Queensferry WwTW | 2987 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330322 | 366357 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DP | CH53DP | ch5 3dp | ch53dp | Flintshire | Sir Y Fflint | Connahs Quay STW | 3734 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329716 | 365684 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DQ | CH53DQ | ch5 3dq | ch53dq | Flintshire | Sir Y Fflint | Queensferry WwTW | 2940 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331461 | 365730 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DR | CH53DR | ch5 3dr | ch53dr | Flintshire | Sir Y Fflint | Queensferry WwTW | 2766 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331328 | 365964 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DS | CH53DS | ch5 3ds | ch53ds | Flintshire | Sir Y Fflint | Queensferry WwTW | 2899 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 330917 | 366020 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DT | CH53DT | ch5 3dt | ch53dt | Flintshire | Sir Y Fflint | Connahs Quay STW | 3077 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329802 | 366335 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DU | CH53DU | ch5 3du | ch53du | Flintshire | Sir Y Fflint | Connahs Quay STW | 2661 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329625 | 366792 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DW | CH53DW | ch5 3dw | ch53dw | Flintshire | Sir Y Fflint | Queensferry WwTW | 2934 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331381 | 365764 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DX | CH53DX | ch5 3dx | ch53dx | Flintshire | Sir Y Fflint | Connahs Quay STW | 3037 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330250 | 366344 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3DY | CH53DY | ch5 3dy | ch53dy | Flintshire | Sir Y Fflint | Connahs Quay STW | 3003 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330161 | 366379 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EA | CH53EA | ch5 3ea | ch53ea | Flintshire | Sir Y Fflint | Connahs Quay STW | 3241 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329010 | 366383 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3ED | CH53ED | ch5 3ed | ch53ed | Flintshire | Sir Y Fflint | Connahs Quay STW | 2940 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330065 | 366446 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EE | CH53EE | ch5 3ee | ch53ee | Flintshire | Sir Y Fflint | Queensferry WwTW | 2767 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331147 | 366045 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EF | CH53EF | ch5 3ef | ch53ef | Flintshire | Sir Y Fflint | Queensferry WwTW | 2713 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331072 | 366146 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EG | CH53EG | ch5 3eg | ch53eg | Flintshire | Sir Y Fflint | Queensferry WwTW | 3021 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331102 | 365785 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EH | CH53EH | ch5 3eh | ch53eh | Flintshire | Sir Y Fflint | Queensferry WwTW | 3034 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 330902 | 365873 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EJ | CH53EJ | ch5 3ej | ch53ej | Flintshire | Sir Y Fflint | Queensferry WwTW | 2999 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 330878 | 365927 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EL | CH53EL | ch5 3el | ch53el | Flintshire | Sir Y Fflint | Queensferry WwTW | 3011 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 330769 | 365979 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EN | CH53EN | ch5 3en | ch53en | Flintshire | Sir Y Fflint | Queensferry WwTW | 2737 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 330634 | 366415 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EP | CH53EP | ch5 3ep | ch53ep | Flintshire | Sir Y Fflint | Queensferry WwTW | 2837 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 330517 | 366383 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EQ | CH53EQ | ch5 3eq | ch53eq | Flintshire | Sir Y Fflint | Queensferry WwTW | 3107 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331044 | 365718 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3ER | CH53ER | ch5 3er | ch53er | Flintshire | Sir Y Fflint | Queensferry WwTW | 2711 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 330616 | 366464 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3ES | CH53ES | ch5 3es | ch53es | Flintshire | Sir Y Fflint | Queensferry WwTW | 2706 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330578 | 366504 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3ET | CH53ET | ch5 3et | ch53et | Flintshire | Sir Y Fflint | Queensferry WwTW | 2776 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330480 | 366498 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EU | CH53EU | ch5 3eu | ch53eu | Flintshire | Sir Y Fflint | Queensferry WwTW | 2225 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330677 | 367090 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EW | CH53EW | ch5 3ew | ch53ew | Flintshire | Sir Y Fflint | Queensferry WwTW | 2900 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330468 | 366342 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EX | CH53EX | ch5 3ex | ch53ex | Flintshire | Sir Y Fflint | Queensferry WwTW | 2159 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330801 | 367050 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EY | CH53EY | ch5 3ey | ch53ey | Flintshire | Sir Y Fflint | Queensferry WwTW | 2191 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330737 | 367073 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3EZ | CH53EZ | ch5 3ez | ch53ez | Flintshire | Sir Y Fflint | Queensferry WwTW | 2313 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330652 | 366985 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3FA | CH53FA | ch5 3fa | ch53fa | Flintshire | Sir Y Fflint | Connahs Quay STW | 3514 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 328109 | 366588 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3FB | CH53FB | ch5 3fb | ch53fb | Flintshire | Sir Y Fflint | Queensferry WwTW | 3265 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 332473 | 365259 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3FE | CH53FE | ch5 3fe | ch53fe | Flintshire | Sir Y Fflint | Queensferry WwTW | 2241 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330636 | 367114 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3FF | CH53FF | ch5 3ff | ch53ff | Flintshire | Sir Y Fflint | Connahs Quay STW | 3084 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330011 | 366306 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3FH | CH53FH | ch5 3fh | ch53fh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3215 | 789 | 700to900 | 1.58 | 1.16 | 0.85 | 14.71 | 7.84 | 8.67 | 330784 | 363619 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3FJ | CH53FJ | ch5 3fj | ch53fj | Flintshire | Sir Y Fflint | Connahs Quay STW | 2806 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329588 | 366652 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3FL | CH53FL | ch5 3fl | ch53fl | Flintshire | Sir Y Fflint | Queensferry WwTW | 2636 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 330777 | 366430 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3FN | CH53FN | ch5 3fn | ch53fn | Flintshire | Sir Y Fflint | Queensferry WwTW | 3980 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 333375 | 364670 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GA | CH53GA | ch5 3ga | ch53ga | Flintshire | Sir Y Fflint | Connahs Quay STW | 3657 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329742 | 365758 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GB | CH53GB | ch5 3gb | ch53gb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3626 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329650 | 365389 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GD | CH53GD | ch5 3gd | ch53gd | Flintshire | Sir Y Fflint | Connahs Quay STW | 3553 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329580 | 365890 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GE | CH53GE | ch5 3ge | ch53ge | Flintshire | Sir Y Fflint | Connahs Quay STW | 3449 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329616 | 365989 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GF | CH53GF | ch5 3gf | ch53gf | Flintshire | Sir Y Fflint | Connahs Quay STW | 3491 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329489 | 365972 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GG | CH53GG | ch5 3gg | ch53gg | Flintshire | Sir Y Fflint | Connahs Quay STW | 3401 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329594 | 366042 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GH | CH53GH | ch5 3gh | ch53gh | Flintshire | Sir Y Fflint | Connahs Quay STW | 3443 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329537 | 366011 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GJ | CH53GJ | ch5 3gj | ch53gj | Flintshire | Sir Y Fflint | Connahs Quay STW | 2607 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329636 | 366845 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GL | CH53GL | ch5 3gl | ch53gl | Flintshire | Sir Y Fflint | Queensferry WwTW | 4053 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 333092 | 364534 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GR | CH53GR | ch5 3gr | ch53gr | Flintshire | Sir Y Fflint | Connahs Quay STW | 3608 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329729 | 365810 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GU | CH53GU | ch5 3gu | ch53gu | Flintshire | Sir Y Fflint | Connahs Quay STW | 3264 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 328849 | 366429 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GW | CH53GW | ch5 3gw | ch53gw | Flintshire | Sir Y Fflint | Connahs Quay STW | 3179 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329151 | 366395 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GX | CH53GX | ch5 3gx | ch53gx | Flintshire | Sir Y Fflint | Queensferry WwTW | 2843 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331703 | 365762 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GY | CH53GY | ch5 3gy | ch53gy | Flintshire | Sir Y Fflint | Connahs Quay STW | 3120 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329179 | 366447 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3GZ | CH53GZ | ch5 3gz | ch53gz | Flintshire | Sir Y Fflint | Queensferry WwTW | 3032 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331055 | 365795 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HA | CH53HA | ch5 3ha | ch53ha | Flintshire | Sir Y Fflint | Connahs Quay STW | 2656 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329377 | 366869 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HB | CH53HB | ch5 3hb | ch53hb | Flintshire | Sir Y Fflint | Queensferry WwTW | 2585 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331420 | 366122 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HD | CH53HD | ch5 3hd | ch53hd | Flintshire | Sir Y Fflint | Queensferry WwTW | 1921 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331460 | 366836 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HE | CH53HE | ch5 3he | ch53he | Flintshire | Sir Y Fflint | Queensferry WwTW | 2185 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331472 | 366535 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HF | CH53HF | ch5 3hf | ch53hf | Flintshire | Sir Y Fflint | Queensferry WwTW | 1879 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331535 | 366844 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HG | CH53HG | ch5 3hg | ch53hg | Flintshire | Sir Y Fflint | Queensferry WwTW | 2412 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331227 | 366404 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HH | CH53HH | ch5 3hh | ch53hh | Flintshire | Sir Y Fflint | Queensferry WwTW | 1979 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331406 | 366799 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HJ | CH53HJ | ch5 3hj | ch53hj | Flintshire | Sir Y Fflint | Queensferry WwTW | 1936 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331379 | 366865 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HL | CH53HL | ch5 3hl | ch53hl | Flintshire | Sir Y Fflint | Queensferry WwTW | 2038 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331345 | 366767 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HN | CH53HN | ch5 3hn | ch53hn | Flintshire | Sir Y Fflint | Queensferry WwTW | 2054 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331398 | 366718 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HP | CH53HP | ch5 3hp | ch53hp | Flintshire | Sir Y Fflint | Queensferry WwTW | 2209 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331226 | 366639 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HQ | CH53HQ | ch5 3hq | ch53hq | Flintshire | Sir Y Fflint | Queensferry WwTW | 2248 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331408 | 366495 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HR | CH53HR | ch5 3hr | ch53hr | Flintshire | Sir Y Fflint | Queensferry WwTW | 2146 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331168 | 366751 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HS | CH53HS | ch5 3hs | ch53hs | Flintshire | Sir Y Fflint | Queensferry WwTW | 2127 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331150 | 366787 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HT | CH53HT | ch5 3ht | ch53ht | Flintshire | Sir Y Fflint | Queensferry WwTW | 2231 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331131 | 366674 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HU | CH53HU | ch5 3hu | ch53hu | Flintshire | Sir Y Fflint | Queensferry WwTW | 1764 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331415 | 367045 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HW | CH53HW | ch5 3hw | ch53hw | Flintshire | Sir Y Fflint | Queensferry WwTW | 2143 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331279 | 366684 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HX | CH53HX | ch5 3hx | ch53hx | Flintshire | Sir Y Fflint | Queensferry WwTW | 1819 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331629 | 366865 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HY | CH53HY | ch5 3hy | ch53hy | Flintshire | Sir Y Fflint | Queensferry WwTW | 1854 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331665 | 366812 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3HZ | CH53HZ | ch5 3hz | ch53hz | Flintshire | Sir Y Fflint | Queensferry WwTW | 1928 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 331646 | 366739 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JA | CH53JA | ch5 3ja | ch53ja | Flintshire | Sir Y Fflint | Connahs Quay STW | 3798 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329840 | 365604 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JB | CH53JB | ch5 3jb | ch53jb | Flintshire | Sir Y Fflint | Queensferry WwTW | 2238 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 331375 | 366523 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JD | CH53JD | ch5 3jd | ch53jd | Flintshire | Sir Y Fflint | Connahs Quay STW | 3200 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330172 | 366182 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JE | CH53JE | ch5 3je | ch53je | Flintshire | Sir Y Fflint | Connahs Quay STW | 3391 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329793 | 366020 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JF | CH53JF | ch5 3jf | ch53jf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3534 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329512 | 365358 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JG | CH53JG | ch5 3jg | ch53jg | Flintshire | Sir Y Fflint | Connahs Quay STW | 3697 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329618 | 365737 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JH | CH53JH | ch5 3jh | ch53jh | Flintshire | Sir Y Fflint | Queensferry WwTW | 3254 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330225 | 366085 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JJ | CH53JJ | ch5 3jj | ch53jj | Flintshire | Sir Y Fflint | Queensferry WwTW | 3252 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330181 | 366127 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JL | CH53JL | ch5 3jl | ch53jl | Flintshire | Sir Y Fflint | Queensferry WwTW | 3157 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330308 | 366141 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JN | CH53JN | ch5 3jn | ch53jn | Flintshire | Sir Y Fflint | Queensferry WwTW | 3246 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330305 | 366027 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JP | CH53JP | ch5 3jp | ch53jp | Flintshire | Sir Y Fflint | Connahs Quay STW | 3737 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329860 | 365664 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JQ | CH53JQ | ch5 3jq | ch53jq | Flintshire | Sir Y Fflint | Queensferry WwTW | 3116 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330335 | 366172 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JR | CH53JR | ch5 3jr | ch53jr | Flintshire | Sir Y Fflint | Connahs Quay STW | 3753 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329751 | 365660 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JS | CH53JS | ch5 3js | ch53js | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3669 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329839 | 365327 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JT | CH53JT | ch5 3jt | ch53jt | Flintshire | Sir Y Fflint | Connahs Quay STW | 3753 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329924 | 365642 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JU | CH53JU | ch5 3ju | ch53ju | Flintshire | Sir Y Fflint | Queensferry WwTW | 3759 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329998 | 365615 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JW | CH53JW | ch5 3jw | ch53jw | Flintshire | Sir Y Fflint | Connahs Quay STW | 3168 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330084 | 366217 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JX | CH53JX | ch5 3jx | ch53jx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3536 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329599 | 365314 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JY | CH53JY | ch5 3jy | ch53jy | Flintshire | Sir Y Fflint | Queensferry WwTW | 3776 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330029 | 365568 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3JZ | CH53JZ | ch5 3jz | ch53jz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3520 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329743 | 365211 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LA | CH53LA | ch5 3la | ch53la | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3402 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329548 | 365189 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LB | CH53LB | ch5 3lb | ch53lb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3366 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329482 | 365184 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LD | CH53LD | ch5 3ld | ch53ld | Flintshire | Sir Y Fflint | Connahs Quay STW | 3656 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329545 | 365792 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LE | CH53LE | ch5 3le | ch53le | Flintshire | Sir Y Fflint | Connahs Quay STW | 3652 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329518 | 365801 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LF | CH53LF | ch5 3lf | ch53lf | Flintshire | Sir Y Fflint | Connahs Quay STW | 3686 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329484 | 365774 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LG | CH53LG | ch5 3lg | ch53lg | Flintshire | Sir Y Fflint | Connahs Quay STW | 3594 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329592 | 365846 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LH | CH53LH | ch5 3lh | ch53lh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3427 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329701 | 365128 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LJ | CH53LJ | ch5 3lj | ch53lj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3440 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329683 | 365155 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LL | CH53LL | ch5 3ll | ch53ll | Flintshire | Sir Y Fflint | Queensferry WwTW | 3037 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331192 | 365728 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LN | CH53LN | ch5 3ln | ch53ln | Flintshire | Sir Y Fflint | Queensferry WwTW | 2807 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331354 | 365910 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LP | CH53LP | ch5 3lp | ch53lp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3447 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329623 | 365198 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LQ | CH53LQ | ch5 3lq | ch53lq | Flintshire | Sir Y Fflint | Connahs Quay STW | 3269 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330139 | 366114 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LR | CH53LR | ch5 3lr | ch53lr | Flintshire | Sir Y Fflint | Queensferry WwTW | 2948 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331201 | 365821 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LS | CH53LS | ch5 3ls | ch53ls | Flintshire | Sir Y Fflint | Queensferry WwTW | 2728 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331215 | 366056 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LT | CH53LT | ch5 3lt | ch53lt | Flintshire | Sir Y Fflint | Queensferry WwTW | 2816 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331516 | 365842 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LU | CH53LU | ch5 3lu | ch53lu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3454 | 789 | 700to900 | 1.58 | 1.16 | 0.85 | 14.71 | 7.84 | 8.67 | 330781 | 364107 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LW | CH53LW | ch5 3lw | ch53lw | Flintshire | Sir Y Fflint | Queensferry WwTW | 2970 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331221 | 365788 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LX | CH53LX | ch5 3lx | ch53lx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3006 | 789 | 700to900 | 1.58 | 1.16 | 0.85 | 14.71 | 7.84 | 8.67 | 330540 | 363636 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LY | CH53LY | ch5 3ly | ch53ly | Flintshire | Sir Y Fflint | Connahs Quay STW | 3275 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329901 | 366124 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3LZ | CH53LZ | ch5 3lz | ch53lz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3044 | 789 | 700to900 | 1.58 | 1.16 | 0.85 | 14.71 | 7.84 | 8.67 | 330628 | 363547 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NA | CH53NA | ch5 3na | ch53na | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2989 | 789 | 700to900 | 1.58 | 1.16 | 0.85 | 14.71 | 7.84 | 8.67 | 330511 | 363654 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NB | CH53NB | ch5 3nb | ch53nb | Flintshire | Sir Y Fflint | Queensferry WwTW | 3006 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331173 | 365770 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3ND | CH53ND | ch5 3nd | ch53nd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3293 | 789 | 700to900 | 1.58 | 1.16 | 0.85 | 14.71 | 7.84 | 8.67 | 330721 | 363899 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NE | CH53NE | ch5 3ne | ch53ne | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 4013 | 789 | 700to900 | 1.58 | 1.16 | 0.85 | 14.71 | 7.84 | 8.67 | 331215 | 364464 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NF | CH53NF | ch5 3nf | ch53nf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3606 | 789 | 700to900 | 1.58 | 1.16 | 0.85 | 14.71 | 7.84 | 8.67 | 330985 | 364069 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NG | CH53NG | ch5 3ng | ch53ng | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3053 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 330249 | 364157 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NH | CH53NH | ch5 3nh | ch53nh | Flintshire | Sir Y Fflint | Connahs Quay STW | 3079 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330164 | 366303 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NJ | CH53NJ | ch5 3nj | ch53nj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3609 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329716 | 365331 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NL | CH53NL | ch5 3nl | ch53nl | Flintshire | Sir Y Fflint | Queensferry WwTW | 2898 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331697 | 365706 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NN | CH53NN | ch5 3nn | ch53nn | Flintshire | Sir Y Fflint | Queensferry WwTW | 2809 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331579 | 365830 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NQ | CH53NQ | ch5 3nq | ch53nq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3508 | 779 | 700to900 | 1.56 | 1.14 | 0.84 | 14.52 | 7.74 | 8.56 | 330504 | 364558 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NR | CH53NR | ch5 3nr | ch53nr | Flintshire | Sir Y Fflint | Queensferry WwTW | 2757 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331589 | 365882 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NS | CH53NS | ch5 3ns | ch53ns | Flintshire | Sir Y Fflint | Queensferry WwTW | 2875 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331718 | 365725 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NT | CH53NT | ch5 3nt | ch53nt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3576 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329702 | 365302 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NU | CH53NU | ch5 3nu | ch53nu | Flintshire | Sir Y Fflint | Queensferry WwTW | 3954 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333747 | 364814 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NW | CH53NW | ch5 3nw | ch53nw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3661 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329809 | 365336 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NX | CH53NX | ch5 3nx | ch53nx | Flintshire | Sir Y Fflint | Queensferry WwTW | 2863 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331635 | 365758 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NY | CH53NY | ch5 3ny | ch53ny | Flintshire | Sir Y Fflint | Queensferry WwTW | 2934 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 332064 | 365606 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3NZ | CH53NZ | ch5 3nz | ch53nz | Flintshire | Sir Y Fflint | Queensferry WwTW | 3085 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 332221 | 365442 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PA | CH53PA | ch5 3pa | ch53pa | Flintshire | Sir Y Fflint | Queensferry WwTW | 2879 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331759 | 365712 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PB | CH53PB | ch5 3pb | ch53pb | Flintshire | Sir Y Fflint | Queensferry WwTW | 3085 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 332221 | 365442 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PD | CH53PD | ch5 3pd | ch53pd | Flintshire | Sir Y Fflint | Queensferry WwTW | 2885 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 332180 | 365645 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PE | CH53PE | ch5 3pe | ch53pe | Flintshire | Sir Y Fflint | Queensferry WwTW | 3030 | 757 | 700to900 | 1.52 | 1.11 | 0.81 | 14.11 | 7.53 | 8.32 | 332237 | 365496 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PF | CH53PF | ch5 3pf | ch53pf | Flintshire | Sir Y Fflint | Queensferry WwTW | 2810 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 332131 | 365724 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PG | CH53PG | ch5 3pg | ch53pg | Flintshire | Sir Y Fflint | Queensferry WwTW | 2080 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 333306 | 366661 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PH | CH53PH | ch5 3ph | ch53ph | Flintshire | Sir Y Fflint | Queensferry WwTW | 2954 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331683 | 365652 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PJ | CH53PJ | ch5 3pj | ch53pj | Flintshire | Sir Y Fflint | Queensferry WwTW | 3921 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 333440 | 364749 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PL | CH53PL | ch5 3pl | ch53pl | Flintshire | Sir Y Fflint | Queensferry WwTW | 3484 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333919 | 365398 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PN | CH53PN | ch5 3pn | ch53pn | Flintshire | Sir Y Fflint | Queensferry WwTW | 2981 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 333259 | 365675 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PP | CH53PP | ch5 3pp | ch53pp | Flintshire | Sir Y Fflint | Queensferry WwTW | 4050 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333607 | 364664 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PQ | CH53PQ | ch5 3pq | ch53pq | Flintshire | Sir Y Fflint | Queensferry WwTW | 2275 | 729 | 700to900 | 1.46 | 1.07 | 0.78 | 13.58 | 7.24 | 8.01 | 332609 | 366259 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PR | CH53PR | ch5 3pr | ch53pr | Flintshire | Sir Y Fflint | Queensferry WwTW | 3500 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 334137 | 365497 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PS | CH53PS | ch5 3ps | ch53ps | Flintshire | Sir Y Fflint | Queensferry WwTW | 3439 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 334145 | 365572 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PT | CH53PT | ch5 3pt | ch53pt | Flintshire | Sir Y Fflint | Queensferry WwTW | 3576 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 334120 | 365400 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PU | CH53PU | ch5 3pu | ch53pu | Flintshire | Sir Y Fflint | Queensferry WwTW | 3551 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333647 | 365206 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PW | CH53PW | ch5 3pw | ch53pw | Flintshire | Sir Y Fflint | Queensferry WwTW | 3672 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333599 | 365060 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PX | CH53PX | ch5 3px | ch53px | Flintshire | Sir Y Fflint | Queensferry WwTW | 2776 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331662 | 365841 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PY | CH53PY | ch5 3py | ch53py | Flintshire | Sir Y Fflint | Queensferry WwTW | 2811 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331711 | 365792 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3PZ | CH53PZ | ch5 3pz | ch53pz | Flintshire | Sir Y Fflint | Queensferry WwTW | 3805 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333813 | 364999 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QB | CH53QB | ch5 3qb | ch53qb | Flintshire | Sir Y Fflint | Queensferry WwTW | 3742 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333909 | 365108 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QD | CH53QD | ch5 3qd | ch53qd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3818 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329932 | 365445 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QE | CH53QE | ch5 3qe | ch53qe | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3729 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329836 | 365399 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QF | CH53QF | ch5 3qf | ch53qf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3779 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329809 | 365474 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QG | CH53QG | ch5 3qg | ch53qg | Flintshire | Sir Y Fflint | Queensferry WwTW | 2956 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331071 | 365872 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QH | CH53QH | ch5 3qh | ch53qh | Flintshire | Sir Y Fflint | Queensferry WwTW | 2989 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331019 | 365862 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QJ | CH53QJ | ch5 3qj | ch53qj | Flintshire | Sir Y Fflint | Queensferry WwTW | 3017 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331001 | 365839 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QL | CH53QL | ch5 3ql | ch53ql | Flintshire | Sir Y Fflint | Queensferry WwTW | 2983 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331058 | 365849 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QN | CH53QN | ch5 3qn | ch53qn | Flintshire | Sir Y Fflint | Queensferry WwTW | 2900 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331268 | 365844 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QP | CH53QP | ch5 3qp | ch53qp | Flintshire | Sir Y Fflint | Queensferry WwTW | 3685 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333772 | 365112 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QQ | CH53QQ | ch5 3qq | ch53qq | Flintshire | Sir Y Fflint | Queensferry WwTW | 2964 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 330990 | 365905 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QR | CH53QR | ch5 3qr | ch53qr | Flintshire | Sir Y Fflint | Queensferry WwTW | 2951 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331287 | 365782 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QS | CH53QS | ch5 3qs | ch53qs | Flintshire | Sir Y Fflint | Connahs Quay STW | 3816 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329796 | 365591 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QT | CH53QT | ch5 3qt | ch53qt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3823 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329814 | 365522 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QU | CH53QU | ch5 3qu | ch53qu | Flintshire | Sir Y Fflint | Queensferry WwTW | 2985 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 331837 | 365588 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QW | CH53QW | ch5 3qw | ch53qw | Flintshire | Sir Y Fflint | Queensferry WwTW | 3838 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333708 | 364923 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QX | CH53QX | ch5 3qx | ch53qx | Flintshire | Sir Y Fflint | Queensferry WwTW | 3692 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333737 | 365090 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QY | CH53QY | ch5 3qy | ch53qy | Flintshire | Sir Y Fflint | Queensferry WwTW | 3856 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333559 | 364852 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3QZ | CH53QZ | ch5 3qz | ch53qz | Flintshire | Sir Y Fflint | Queensferry WwTW | 3859 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333625 | 364871 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RA | CH53RA | ch5 3ra | ch53ra | Flintshire | Sir Y Fflint | Connahs Quay STW | 2866 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330044 | 366522 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RB | CH53RB | ch5 3rb | ch53rb | Flintshire | Sir Y Fflint | Connahs Quay STW | 2710 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330055 | 366677 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RD | CH53RD | ch5 3rd | ch53rd | Flintshire | Sir Y Fflint | Connahs Quay STW | 2790 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330055 | 366597 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RE | CH53RE | ch5 3re | ch53re | Flintshire | Sir Y Fflint | Connahs Quay STW | 2694 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330111 | 366690 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RF | CH53RF | ch5 3rf | ch53rf | Flintshire | Sir Y Fflint | Connahs Quay STW | 2875 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330204 | 366506 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RG | CH53RG | ch5 3rg | ch53rg | Flintshire | Sir Y Fflint | Connahs Quay STW | 2828 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330093 | 366557 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RH | CH53RH | ch5 3rh | ch53rh | Flintshire | Sir Y Fflint | Connahs Quay STW | 2860 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330244 | 366521 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RJ | CH53RJ | ch5 3rj | ch53rj | Flintshire | Sir Y Fflint | Connahs Quay STW | 2685 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330172 | 366697 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RL | CH53RL | ch5 3rl | ch53rl | Flintshire | Sir Y Fflint | Connahs Quay STW | 2794 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330211 | 366587 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RN | CH53RN | ch5 3rn | ch53rn | Flintshire | Sir Y Fflint | Connahs Quay STW | 2853 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330278 | 366528 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RP | CH53RP | ch5 3rp | ch53rp | Flintshire | Sir Y Fflint | Connahs Quay STW | 2945 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330262 | 366436 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RQ | CH53RQ | ch5 3rq | ch53rq | Flintshire | Sir Y Fflint | Connahs Quay STW | 2771 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330268 | 366610 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RR | CH53RR | ch5 3rr | ch53rr | Flintshire | Sir Y Fflint | Connahs Quay STW | 2675 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330210 | 366706 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RS | CH53RS | ch5 3rs | ch53rs | Flintshire | Sir Y Fflint | Connahs Quay STW | 2771 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329969 | 366623 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RT | CH53RT | ch5 3rt | ch53rt | Flintshire | Sir Y Fflint | Connahs Quay STW | 2931 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330168 | 366451 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RU | CH53RU | ch5 3ru | ch53ru | Flintshire | Sir Y Fflint | Connahs Quay STW | 2841 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 329895 | 366561 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RW | CH53RW | ch5 3rw | ch53rw | Flintshire | Sir Y Fflint | Connahs Quay STW | 2679 | 769 | 700to900 | 1.54 | 1.13 | 0.83 | 14.33 | 7.64 | 8.45 | 330284 | 366702 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RX | CH53RX | ch5 3rx | ch53rx | Flintshire | Sir Y Fflint | Connahs Quay STW | 3129 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329686 | 366302 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RY | CH53RY | ch5 3ry | ch53ry | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3297 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329642 | 365012 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3RZ | CH53RZ | ch5 3rz | ch53rz | Flintshire | Sir Y Fflint | Queensferry WwTW | 2819 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 331199 | 365963 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SA | CH53SA | ch5 3sa | ch53sa | Flintshire | Sir Y Fflint | Connahs Quay STW | 3471 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330053 | 365915 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SB | CH53SB | ch5 3sb | ch53sb | Flintshire | Sir Y Fflint | Connahs Quay STW | 3416 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329986 | 365975 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SD | CH53SD | ch5 3sd | ch53sd | Flintshire | Sir Y Fflint | Connahs Quay STW | 3349 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329978 | 366042 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SE | CH53SE | ch5 3se | ch53se | Flintshire | Sir Y Fflint | Connahs Quay STW | 3494 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329975 | 365897 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SF | CH53SF | ch5 3sf | ch53sf | Flintshire | Sir Y Fflint | Connahs Quay STW | 3594 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329867 | 365807 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SG | CH53SG | ch5 3sg | ch53sg | Flintshire | Sir Y Fflint | Queensferry WwTW | 3431 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330144 | 365921 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SH | CH53SH | ch5 3sh | ch53sh | Flintshire | Sir Y Fflint | Queensferry WwTW | 3515 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330078 | 365866 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SJ | CH53SJ | ch5 3sj | ch53sj | Flintshire | Sir Y Fflint | Connahs Quay STW | 3323 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330086 | 366062 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SL | CH53SL | ch5 3sl | ch53sl | Flintshire | Sir Y Fflint | Queensferry WwTW | 3569 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330086 | 365788 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SN | CH53SN | ch5 3sn | ch53sn | Flintshire | Sir Y Fflint | Queensferry WwTW | 3558 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333621 | 365189 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SP | CH53SP | ch5 3sp | ch53sp | Flintshire | Sir Y Fflint | Queensferry WwTW | 3506 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333687 | 365270 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SQ | CH53SQ | ch5 3sq | ch53sq | Flintshire | Sir Y Fflint | Connahs Quay STW | 3613 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 330012 | 365775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SR | CH53SR | ch5 3sr | ch53sr | Flintshire | Sir Y Fflint | Queensferry WwTW | 3430 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333804 | 365403 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SS | CH53SS | ch5 3ss | ch53ss | Flintshire | Sir Y Fflint | Connahs Quay STW | 3555 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329763 | 365858 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3ST | CH53ST | ch5 3st | ch53st | Flintshire | Sir Y Fflint | Queensferry WwTW | 3556 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333880 | 365300 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3SW | CH53SW | ch5 3sw | ch53sw | Flintshire | Sir Y Fflint | Queensferry WwTW | 3607 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 334193 | 365406 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TA | CH53TA | ch5 3ta | ch53ta | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3747 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329511 | 365597 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TB | CH53TB | ch5 3tb | ch53tb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3620 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329483 | 365469 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TD | CH53TD | ch5 3td | ch53td | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3632 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329466 | 365491 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TE | CH53TE | ch5 3te | ch53te | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3690 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329446 | 365564 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TF | CH53TF | ch5 3tf | ch53tf | Flintshire | Sir Y Fflint | Connahs Quay STW | 3727 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329441 | 365741 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TG | CH53TG | ch5 3tg | ch53tg | Flintshire | Sir Y Fflint | Connahs Quay STW | 3748 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329519 | 365703 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TH | CH53TH | ch5 3th | ch53th | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3735 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329390 | 365639 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TJ | CH53TJ | ch5 3tj | ch53tj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3629 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329363 | 365535 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TL | CH53TL | ch5 3tl | ch53tl | Flintshire | Sir Y Fflint | Queensferry WwTW | 2152 | 751 | 700to900 | 1.5 | 1.1 | 0.81 | 14 | 7.47 | 8.25 | 330843 | 367016 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TN | CH53TN | ch5 3tn | ch53tn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3674 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329372 | 365580 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TP | CH53TP | ch5 3tp | ch53tp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3588 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329285 | 365524 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TQ | CH53TQ | ch5 3tq | ch53tq | Flintshire | Sir Y Fflint | Connahs Quay STW | 3725 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329413 | 365749 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TR | CH53TR | ch5 3tr | ch53tr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3631 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329387 | 365527 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TS | CH53TS | ch5 3ts | ch53ts | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3517 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329314 | 365435 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TT | CH53TT | ch5 3tt | ch53tt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3554 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329438 | 365418 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TU | CH53TU | ch5 3tu | ch53tu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3467 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329387 | 365346 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TW | CH53TW | ch5 3tw | ch53tw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3772 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329307 | 365714 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TX | CH53TX | ch5 3tx | ch53tx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3671 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329269 | 365621 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TY | CH53TY | ch5 3ty | ch53ty | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3438 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329416 | 365299 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3TZ | CH53TZ | ch5 3tz | ch53tz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3715 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329233 | 365682 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UA | CH53UA | ch5 3ua | ch53ua | Flintshire | Sir Y Fflint | Connahs Quay STW | 3584 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329397 | 365898 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UB | CH53UB | ch5 3ub | ch53ub | Flintshire | Sir Y Fflint | Connahs Quay STW | 3545 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329408 | 365935 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UD | CH53UD | ch5 3ud | ch53ud | Flintshire | Sir Y Fflint | Connahs Quay STW | 3565 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329489 | 365896 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UE | CH53UE | ch5 3ue | ch53ue | Flintshire | Sir Y Fflint | Connahs Quay STW | 3621 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329463 | 365845 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UF | CH53UF | ch5 3uf | ch53uf | Flintshire | Sir Y Fflint | Connahs Quay STW | 3737 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329305 | 365763 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UG | CH53UG | ch5 3ug | ch53ug | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3668 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329193 | 365647 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UH | CH53UH | ch5 3uh | ch53uh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3748 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329160 | 365745 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UJ | CH53UJ | ch5 3uj | ch53uj | Flintshire | Sir Y Fflint | Connahs Quay STW | 3760 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329163 | 365779 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UL | CH53UL | ch5 3ul | ch53ul | Flintshire | Sir Y Fflint | Connahs Quay STW | 3650 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329305 | 365853 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UN | CH53UN | ch5 3un | ch53un | Flintshire | Sir Y Fflint | Connahs Quay STW | 3562 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329254 | 365958 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UP | CH53UP | ch5 3up | ch53up | Flintshire | Sir Y Fflint | Connahs Quay STW | 3659 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329159 | 365886 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UQ | CH53UQ | ch5 3uq | ch53uq | Flintshire | Sir Y Fflint | Connahs Quay STW | 3597 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329152 | 365953 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UR | CH53UR | ch5 3ur | ch53ur | Flintshire | Sir Y Fflint | Connahs Quay STW | 3528 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329176 | 366018 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3US | CH53US | ch5 3us | ch53us | Flintshire | Sir Y Fflint | Queensferry WwTW | 4106 | 721 | 700to900 | 1.44 | 1.06 | 0.77 | 13.43 | 7.16 | 7.92 | 333981 | 364743 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UT | CH53UT | ch5 3ut | ch53ut | Flintshire | Sir Y Fflint | Connahs Quay STW | 3563 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329319 | 365939 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UU | CH53UU | ch5 3uu | ch53uu | Flintshire | Sir Y Fflint | Connahs Quay STW | 3593 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329414 | 365884 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UW | CH53UW | ch5 3uw | ch53uw | Flintshire | Sir Y Fflint | Connahs Quay STW | 3269 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329777 | 366145 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UX | CH53UX | ch5 3ux | ch53ux | Flintshire | Sir Y Fflint | Connahs Quay STW | 3448 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329345 | 366051 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UY | CH53UY | ch5 3uy | ch53uy | Flintshire | Sir Y Fflint | Connahs Quay STW | 3630 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329361 | 365859 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3UZ | CH53UZ | ch5 3uz | ch53uz | Flintshire | Sir Y Fflint | Connahs Quay STW | 3120 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329779 | 366295 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3XA | CH53XA | ch5 3xa | ch53xa | Flintshire | Sir Y Fflint | Connahs Quay STW | 3317 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329483 | 366152 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3XB | CH53XB | ch5 3xb | ch53xb | Flintshire | Sir Y Fflint | Connahs Quay STW | 3255 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329733 | 366166 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3XD | CH53XD | ch5 3xd | ch53xd | Flintshire | Sir Y Fflint | Connahs Quay STW | 3316 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329423 | 366167 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3XF | CH53XF | ch5 3xf | ch53xf | Flintshire | Sir Y Fflint | Connahs Quay STW | 3248 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329489 | 366221 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3XG | CH53XG | ch5 3xg | ch53xg | Flintshire | Sir Y Fflint | Connahs Quay STW | 3216 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329783 | 366198 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3XJ | CH53XJ | ch5 3xj | ch53xj | Flintshire | Sir Y Fflint | Connahs Quay STW | 3294 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329523 | 366166 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3XL | CH53XL | ch5 3xl | ch53xl | Flintshire | Sir Y Fflint | Connahs Quay STW | 3214 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329825 | 366194 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3XN | CH53XN | ch5 3xn | ch53xn | Flintshire | Sir Y Fflint | Connahs Quay STW | 3482 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329372 | 366009 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3XP | CH53XP | ch5 3xp | ch53xp | Flintshire | Sir Y Fflint | Connahs Quay STW | 3251 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329547 | 366205 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3XQ | CH53XQ | ch5 3xq | ch53xq | Flintshire | Sir Y Fflint | Connahs Quay STW | 3215 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329891 | 366185 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3YB | CH53YB | ch5 3yb | ch53yb | Flintshire | Sir Y Fflint | Connahs Quay STW | 2985 | 781 | 700to900 | 1.56 | 1.14 | 0.84 | 14.56 | 7.76 | 8.58 | 329755 | 366436 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 3YE | CH53YE | ch5 3ye | ch53ye | Flintshire | Sir Y Fflint | Connahs Quay STW | 3318 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 329389 | 366174 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AB | CH54AB | ch5 4ab | ch54ab | Flintshire | Sir Y Fflint | Connahs Quay STW | 1095 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329255 | 369858 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AD | CH54AD | ch5 4ad | ch54ad | Flintshire | Sir Y Fflint | Connahs Quay STW | 1151 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329194 | 369860 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AE | CH54AE | ch5 4ae | ch54ae | Flintshire | Sir Y Fflint | Connahs Quay STW | 1146 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329160 | 369761 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AF | CH54AF | ch5 4af | ch54af | Flintshire | Sir Y Fflint | Connahs Quay STW | 1143 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329174 | 369792 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AG | CH54AG | ch5 4ag | ch54ag | Flintshire | Sir Y Fflint | Connahs Quay STW | 1328 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329046 | 369960 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AH | CH54AH | ch5 4ah | ch54ah | Flintshire | Sir Y Fflint | Connahs Quay STW | 1246 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329133 | 369951 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AJ | CH54AJ | ch5 4aj | ch54aj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1551 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328852 | 370070 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AL | CH54AL | ch5 4al | ch54al | Flintshire | Sir Y Fflint | Connahs Quay STW | 1401 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328881 | 369717 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AN | CH54AN | ch5 4an | ch54an | Flintshire | Sir Y Fflint | Connahs Quay STW | 1239 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329090 | 369841 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AP | CH54AP | ch5 4ap | ch54ap | Flintshire | Sir Y Fflint | Connahs Quay STW | 1291 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329001 | 369742 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AQ | CH54AQ | ch5 4aq | ch54aq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1441 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328955 | 370031 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AR | CH54AR | ch5 4ar | ch54ar | Flintshire | Sir Y Fflint | Connahs Quay STW | 1647 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328802 | 370182 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AS | CH54AS | ch5 4as | ch54as | Flintshire | Sir Y Fflint | Connahs Quay STW | 1889 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328565 | 370252 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AT | CH54AT | ch5 4at | ch54at | Flintshire | Sir Y Fflint | Connahs Quay STW | 1171 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329126 | 369739 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AU | CH54AU | ch5 4au | ch54au | Flintshire | Sir Y Fflint | Connahs Quay STW | 1221 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329063 | 369704 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AW | CH54AW | ch5 4aw | ch54aw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1281 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329029 | 369797 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AX | CH54AX | ch5 4ax | ch54ax | Flintshire | Sir Y Fflint | Connahs Quay STW | 1285 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329098 | 369968 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AY | CH54AY | ch5 4ay | ch54ay | Flintshire | Sir Y Fflint | Connahs Quay STW | 1400 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329002 | 370032 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4AZ | CH54AZ | ch5 4az | ch54az | Flintshire | Sir Y Fflint | Connahs Quay STW | 1522 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328902 | 370105 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BA | CH54BA | ch5 4ba | ch54ba | Flintshire | Sir Y Fflint | Connahs Quay STW | 1574 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328864 | 370144 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BB | CH54BB | ch5 4bb | ch54bb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1863 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328557 | 370178 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BD | CH54BD | ch5 4bd | ch54bd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1368 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328902 | 369665 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BE | CH54BE | ch5 4be | ch54be | Flintshire | Sir Y Fflint | Connahs Quay STW | 1977 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328407 | 370120 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BG | CH54BG | ch5 4bg | ch54bg | Flintshire | Sir Y Fflint | Connahs Quay STW | 1990 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328332 | 369943 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BH | CH54BH | ch5 4bh | ch54bh | Flintshire | Sir Y Fflint | Connahs Quay STW | 2128 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328251 | 370135 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BJ | CH54BJ | ch5 4bj | ch54bj | Flintshire | Sir Y Fflint | Connahs Quay STW | 2339 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 328208 | 370536 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BL | CH54BL | ch5 4bl | ch54bl | Flintshire | Sir Y Fflint | Connahs Quay STW | 2617 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 327945 | 370636 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BN | CH54BN | ch5 4bn | ch54bn | Flintshire | Sir Y Fflint | Connahs Quay STW | 1826 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328586 | 370152 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BP | CH54BP | ch5 4bp | ch54bp | Flintshire | Sir Y Fflint | Connahs Quay STW | 2848 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 327955 | 371079 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BQ | CH54BQ | ch5 4bq | ch54bq | Flintshire | Sir Y Fflint | Connahs Quay STW | 2034 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328325 | 370063 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BR | CH54BR | ch5 4br | ch54br | Flintshire | Sir Y Fflint | Connahs Quay STW | 2377 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328106 | 370425 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BS | CH54BS | ch5 4bs | ch54bs | Flintshire | Sir Y Fflint | Connahs Quay STW | 1358 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329008 | 369949 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BT | CH54BT | ch5 4bt | ch54bt | Flintshire | Sir Y Fflint | Connahs Quay STW | 787 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329909 | 368666 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BU | CH54BU | ch5 4bu | ch54bu | Flintshire | Sir Y Fflint | Connahs Quay STW | 1992 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328344 | 369990 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BW | CH54BW | ch5 4bw | ch54bw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1729 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328520 | 369554 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BX | CH54BX | ch5 4bx | ch54bx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1907 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328452 | 370041 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BY | CH54BY | ch5 4by | ch54by | Flintshire | Sir Y Fflint | Connahs Quay STW | 2039 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328359 | 370165 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4BZ | CH54BZ | ch5 4bz | ch54bz | Flintshire | Sir Y Fflint | Connahs Quay STW | 2081 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328307 | 370150 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DA | CH54DA | ch5 4da | ch54da | Flintshire | Sir Y Fflint | Connahs Quay STW | 232 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330245 | 369148 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DB | CH54DB | ch5 4db | ch54db | Flintshire | Sir Y Fflint | Connahs Quay STW | 858 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329451 | 369717 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DD | CH54DD | ch5 4dd | ch54dd | Flintshire | Sir Y Fflint | Connahs Quay STW | 190 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330135 | 369222 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DF | CH54DF | ch5 4df | ch54df | Flintshire | Sir Y Fflint | Connahs Quay STW | 234 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330017 | 369309 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DG | CH54DG | ch5 4dg | ch54dg | Flintshire | Sir Y Fflint | Connahs Quay STW | 2092 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328265 | 370068 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DH | CH54DH | ch5 4dh | ch54dh | Flintshire | Sir Y Fflint | Connahs Quay STW | 456 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329794 | 369474 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DJ | CH54DJ | ch5 4dj | ch54dj | Flintshire | Sir Y Fflint | Connahs Quay STW | 696 | 727 | 700to900 | 1.45 | 1.06 | 0.78 | 13.55 | 7.22 | 7.98 | 329579 | 369598 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DL | CH54DL | ch5 4dl | ch54dl | Flintshire | Sir Y Fflint | Connahs Quay STW | 933 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329371 | 369720 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DN | CH54DN | ch5 4dn | ch54dn | Flintshire | Sir Y Fflint | Connahs Quay STW | 1775 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328482 | 369621 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DP | CH54DP | ch5 4dp | ch54dp | Flintshire | Sir Y Fflint | Connahs Quay STW | 820 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329483 | 369695 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DQ | CH54DQ | ch5 4dq | ch54dq | Flintshire | Sir Y Fflint | Connahs Quay STW | 362 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329878 | 369380 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DR | CH54DR | ch5 4dr | ch54dr | Flintshire | Sir Y Fflint | Connahs Quay STW | 1007 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329322 | 369793 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DS | CH54DS | ch5 4ds | ch54ds | Flintshire | Sir Y Fflint | Connahs Quay STW | 623 | 727 | 700to900 | 1.45 | 1.06 | 0.78 | 13.55 | 7.22 | 7.98 | 329758 | 369775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DT | CH54DT | ch5 4dt | ch54dt | Flintshire | Sir Y Fflint | Connahs Quay STW | 2145 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328177 | 369963 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DU | CH54DU | ch5 4du | ch54du | Flintshire | Sir Y Fflint | Connahs Quay STW | 594 | 727 | 700to900 | 1.45 | 1.06 | 0.78 | 13.55 | 7.22 | 7.98 | 329687 | 369597 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DW | CH54DW | ch5 4dw | ch54dw | Flintshire | Sir Y Fflint | Connahs Quay STW | 913 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329394 | 369723 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DX | CH54DX | ch5 4dx | ch54dx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1008 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329303 | 369750 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DY | CH54DY | ch5 4dy | ch54dy | Flintshire | Sir Y Fflint | Connahs Quay STW | 992 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329320 | 369751 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4DZ | CH54DZ | ch5 4dz | ch54dz | Flintshire | Sir Y Fflint | Connahs Quay STW | 976 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329322 | 369711 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EA | CH54EA | ch5 4ea | ch54ea | Flintshire | Sir Y Fflint | Connahs Quay STW | 2632 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328003 | 367994 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EB | CH54EB | ch5 4eb | ch54eb | Flintshire | Sir Y Fflint | Connahs Quay STW | 581 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329664 | 369456 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4ED | CH54ED | ch5 4ed | ch54ed | Flintshire | Sir Y Fflint | Connahs Quay STW | 629 | 727 | 700to900 | 1.45 | 1.06 | 0.78 | 13.55 | 7.22 | 7.98 | 329627 | 369518 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EE | CH54EE | ch5 4ee | ch54ee | Flintshire | Sir Y Fflint | Connahs Quay STW | 466 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329789 | 369498 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EF | CH54EF | ch5 4ef | ch54ef | Flintshire | Sir Y Fflint | Connahs Quay STW | 428 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329828 | 369496 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EG | CH54EG | ch5 4eg | ch54eg | Flintshire | Sir Y Fflint | Connahs Quay STW | 514 | 727 | 700to900 | 1.45 | 1.06 | 0.78 | 13.55 | 7.22 | 7.98 | 329754 | 369547 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EH | CH54EH | ch5 4eh | ch54eh | Flintshire | Sir Y Fflint | Connahs Quay STW | 329 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329915 | 369429 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EJ | CH54EJ | ch5 4ej | ch54ej | Flintshire | Sir Y Fflint | Connahs Quay STW | 164 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330081 | 369342 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EL | CH54EL | ch5 4el | ch54el | Flintshire | Sir Y Fflint | Connahs Quay STW | 1036 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329368 | 368822 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EP | CH54EP | ch5 4ep | ch54ep | Flintshire | Sir Y Fflint | Connahs Quay STW | 1268 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329021 | 369031 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EQ | CH54EQ | ch5 4eq | ch54eq | Flintshire | Sir Y Fflint | Connahs Quay STW | 300 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329943 | 369424 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4ER | CH54ER | ch5 4er | ch54er | Flintshire | Sir Y Fflint | Connahs Quay STW | 182 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330060 | 369352 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4ES | CH54ES | ch5 4es | ch54es | Flintshire | Sir Y Fflint | Connahs Quay STW | 2616 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 327975 | 368073 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4ET | CH54ET | ch5 4et | ch54et | Flintshire | Sir Y Fflint | Connahs Quay STW | 863 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329453 | 369733 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EU | CH54EU | ch5 4eu | ch54eu | Flintshire | Sir Y Fflint | Connahs Quay STW | 780 | 727 | 700to900 | 1.45 | 1.06 | 0.78 | 13.55 | 7.22 | 7.98 | 329525 | 369692 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EW | CH54EW | ch5 4ew | ch54ew | Flintshire | Sir Y Fflint | Connahs Quay STW | 208 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330035 | 369415 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EX | CH54EX | ch5 4ex | ch54ex | Flintshire | Sir Y Fflint | Connahs Quay STW | 2019 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328398 | 370205 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EY | CH54EY | ch5 4ey | ch54ey | Flintshire | Sir Y Fflint | Connahs Quay STW | 784 | 727 | 700to900 | 1.45 | 1.06 | 0.78 | 13.55 | 7.22 | 7.98 | 329518 | 369684 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4EZ | CH54EZ | ch5 4ez | ch54ez | Flintshire | Sir Y Fflint | Connahs Quay STW | 751 | 727 | 700to900 | 1.45 | 1.06 | 0.78 | 13.55 | 7.22 | 7.98 | 329544 | 369661 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FD | CH54FD | ch5 4fd | ch54fd | Flintshire | Sir Y Fflint | Connahs Quay STW | 908 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329503 | 368851 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FE | CH54FE | ch5 4fe | ch54fe | Flintshire | Sir Y Fflint | Connahs Quay STW | 2589 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 327987 | 368106 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FF | CH54FF | ch5 4ff | ch54ff | Flintshire | Sir Y Fflint | Connahs Quay STW | 2474 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328053 | 368226 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FG | CH54FG | ch5 4fg | ch54fg | Flintshire | Sir Y Fflint | Connahs Quay STW | 462 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329815 | 369198 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FH | CH54FH | ch5 4fh | ch54fh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1345 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328904 | 369225 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FJ | CH54FJ | ch5 4fj | ch54fj | Flintshire | Sir Y Fflint | Connahs Quay STW | 2201 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328087 | 368926 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FL | CH54FL | ch5 4fl | ch54fl | Flintshire | Sir Y Fflint | Connahs Quay STW | 125 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330163 | 369281 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FN | CH54FN | ch5 4fn | ch54fn | Flintshire | Sir Y Fflint | Connahs Quay STW | 920 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329374 | 369689 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FP | CH54FP | ch5 4fp | ch54fp | Flintshire | Sir Y Fflint | Connahs Quay STW | 2530 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328022 | 368165 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FQ | CH54FQ | ch5 4fq | ch54fq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1346 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328994 | 369888 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FT | CH54FT | ch5 4ft | ch54ft | Flintshire | Sir Y Fflint | Connahs Quay STW | 1787 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328728 | 368428 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FW | CH54FW | ch5 4fw | ch54fw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1866 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328611 | 368471 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FX | CH54FX | ch5 4fx | ch54fx | Flintshire | Sir Y Fflint | Connahs Quay STW | 2207 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328143 | 368694 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FY | CH54FY | ch5 4fy | ch54fy | Flintshire | Sir Y Fflint | Connahs Quay STW | 1912 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328563 | 368464 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4FZ | CH54FZ | ch5 4fz | ch54fz | Flintshire | Sir Y Fflint | Connahs Quay STW | 2023 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328429 | 368480 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GA | CH54GA | ch5 4ga | ch54ga | Flintshire | Sir Y Fflint | Connahs Quay STW | 1995 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328434 | 368533 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GB | CH54GB | ch5 4gb | ch54gb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1909 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328525 | 368543 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GD | CH54GD | ch5 4gd | ch54gd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1886 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328539 | 368568 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GE | CH54GE | ch5 4ge | ch54ge | Flintshire | Sir Y Fflint | Connahs Quay STW | 1684 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328819 | 368477 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GF | CH54GF | ch5 4gf | ch54gf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1844 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328565 | 368610 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GG | CH54GG | ch5 4gg | ch54gg | Flintshire | Sir Y Fflint | Connahs Quay STW | 1722 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328522 | 369488 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GH | CH54GH | ch5 4gh | ch54gh | Flintshire | Sir Y Fflint | Connahs Quay STW | 2589 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328061 | 367983 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GJ | CH54GJ | ch5 4gj | ch54gj | Flintshire | Sir Y Fflint | Connahs Quay STW | 2554 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328107 | 367977 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GL | CH54GL | ch5 4gl | ch54gl | Flintshire | Sir Y Fflint | Connahs Quay STW | 2670 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328013 | 367908 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GN | CH54GN | ch5 4gn | ch54gn | Flintshire | Sir Y Fflint | Connahs Quay STW | 2580 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328114 | 367919 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GP | CH54GP | ch5 4gp | ch54gp | Flintshire | Sir Y Fflint | Connahs Quay STW | 2624 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328068 | 367910 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GQ | CH54GQ | ch5 4gq | ch54gq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1846 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328671 | 368408 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GR | CH54GR | ch5 4gr | ch54gr | Flintshire | Sir Y Fflint | Connahs Quay STW | 2660 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328071 | 367841 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GS | CH54GS | ch5 4gs | ch54gs | Flintshire | Sir Y Fflint | Connahs Quay STW | 2683 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328091 | 367776 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GT | CH54GT | ch5 4gt | ch54gt | Flintshire | Sir Y Fflint | Connahs Quay STW | 2672 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328132 | 367739 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GU | CH54GU | ch5 4gu | ch54gu | Flintshire | Sir Y Fflint | Connahs Quay STW | 2617 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328161 | 367792 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GW | CH54GW | ch5 4gw | ch54gw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1726 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328515 | 369388 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GX | CH54GX | ch5 4gx | ch54gx | Flintshire | Sir Y Fflint | Connahs Quay STW | 2593 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328128 | 367878 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GY | CH54GY | ch5 4gy | ch54gy | Flintshire | Sir Y Fflint | Connahs Quay STW | 1652 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328590 | 369319 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4GZ | CH54GZ | ch5 4gz | ch54gz | Flintshire | Sir Y Fflint | Connahs Quay STW | 1692 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328549 | 369396 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HA | CH54HA | ch5 4ha | ch54ha | Flintshire | Sir Y Fflint | Connahs Quay STW | 386 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330102 | 369020 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HD | CH54HD | ch5 4hd | ch54hd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1915 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328631 | 368343 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HE | CH54HE | ch5 4he | ch54he | Flintshire | Sir Y Fflint | Connahs Quay STW | 1684 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328805 | 368499 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HF | CH54HF | ch5 4hf | ch54hf | Flintshire | Sir Y Fflint | Connahs Quay STW | 502 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330074 | 368906 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HG | CH54HG | ch5 4hg | ch54hg | Flintshire | Sir Y Fflint | Connahs Quay STW | 589 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330079 | 368814 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HH | CH54HH | ch5 4hh | ch54hh | Flintshire | Sir Y Fflint | Connahs Quay STW | 2212 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328616 | 367879 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HJ | CH54HJ | ch5 4hj | ch54hj | Flintshire | Sir Y Fflint | Connahs Quay STW | 761 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329881 | 368709 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HL | CH54HL | ch5 4hl | ch54hl | Flintshire | Sir Y Fflint | Connahs Quay STW | 1076 | 752 | 700to900 | 1.51 | 1.1 | 0.81 | 14.02 | 7.48 | 8.26 | 329630 | 368494 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HN | CH54HN | ch5 4hn | ch54hn | Flintshire | Sir Y Fflint | Connahs Quay STW | 686 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329898 | 368786 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HP | CH54HP | ch5 4hp | ch54hp | Flintshire | Sir Y Fflint | Connahs Quay STW | 779 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329810 | 368731 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HQ | CH54HQ | ch5 4hq | ch54hq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1968 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328541 | 368388 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HR | CH54HR | ch5 4hr | ch54hr | Flintshire | Sir Y Fflint | Connahs Quay STW | 814 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329791 | 368701 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HS | CH54HS | ch5 4hs | ch54hs | Flintshire | Sir Y Fflint | Connahs Quay STW | 909 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329731 | 368627 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HT | CH54HT | ch5 4ht | ch54ht | Flintshire | Sir Y Fflint | Connahs Quay STW | 951 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329675 | 368615 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HU | CH54HU | ch5 4hu | ch54hu | Flintshire | Sir Y Fflint | Connahs Quay STW | 1028 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329582 | 368591 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HW | CH54HW | ch5 4hw | ch54hw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1081 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329585 | 368521 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HX | CH54HX | ch5 4hx | ch54hx | Flintshire | Sir Y Fflint | Connahs Quay STW | 941 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329596 | 368694 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HY | CH54HY | ch5 4hy | ch54hy | Flintshire | Sir Y Fflint | Connahs Quay STW | 2510 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328255 | 367845 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4HZ | CH54HZ | ch5 4hz | ch54hz | Flintshire | Sir Y Fflint | Connahs Quay STW | 1040 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329485 | 368665 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JA | CH54JA | ch5 4ja | ch54ja | Flintshire | Sir Y Fflint | Connahs Quay STW | 1051 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329438 | 368702 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JB | CH54JB | ch5 4jb | ch54jb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1031 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329538 | 368625 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JD | CH54JD | ch5 4jd | ch54jd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1045 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329503 | 368639 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JE | CH54JE | ch5 4je | ch54je | Flintshire | Sir Y Fflint | Connahs Quay STW | 774 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329758 | 368775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JF | CH54JF | ch5 4jf | ch54jf | Flintshire | Sir Y Fflint | Connahs Quay STW | 745 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329805 | 368775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JG | CH54JG | ch5 4jg | ch54jg | Flintshire | Sir Y Fflint | Connahs Quay STW | 1897 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328379 | 369747 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JH | CH54JH | ch5 4jh | ch54jh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1947 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328351 | 369848 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JJ | CH54JJ | ch5 4jj | ch54jj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1900 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328409 | 369884 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JL | CH54JL | ch5 4jl | ch54jl | Flintshire | Sir Y Fflint | Connahs Quay STW | 1243 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329291 | 368578 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JN | CH54JN | ch5 4jn | ch54jn | Flintshire | Sir Y Fflint | Connahs Quay STW | 1812 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328509 | 369913 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JP | CH54JP | ch5 4jp | ch54jp | Flintshire | Sir Y Fflint | Connahs Quay STW | 1862 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328812 | 368186 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JQ | CH54JQ | ch5 4jq | ch54jq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1824 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328454 | 369748 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JR | CH54JR | ch5 4jr | ch54jr | Flintshire | Sir Y Fflint | Connahs Quay STW | 1529 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 329105 | 368357 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JS | CH54JS | ch5 4js | ch54js | Flintshire | Sir Y Fflint | Connahs Quay STW | 1494 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 329104 | 368411 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JT | CH54JT | ch5 4jt | ch54jt | Flintshire | Sir Y Fflint | Connahs Quay STW | 1846 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328902 | 368109 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JU | CH54JU | ch5 4ju | ch54ju | Flintshire | Sir Y Fflint | Connahs Quay STW | 1829 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328878 | 368160 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JW | CH54JW | ch5 4jw | ch54jw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1790 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328495 | 369775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JX | CH54JX | ch5 4jx | ch54jx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1323 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329061 | 368781 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JY | CH54JY | ch5 4jy | ch54jy | Flintshire | Sir Y Fflint | Connahs Quay STW | 1182 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329156 | 368909 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4JZ | CH54JZ | ch5 4jz | ch54jz | Flintshire | Sir Y Fflint | Connahs Quay STW | 1458 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328890 | 368830 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LA | CH54LA | ch5 4la | ch54la | Flintshire | Sir Y Fflint | Connahs Quay STW | 1773 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328886 | 368236 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LB | CH54LB | ch5 4lb | ch54lb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1281 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329240 | 368580 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LD | CH54LD | ch5 4ld | ch54ld | Flintshire | Sir Y Fflint | Connahs Quay STW | 1216 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329274 | 368642 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LE | CH54LE | ch5 4le | ch54le | Flintshire | Sir Y Fflint | Connahs Quay STW | 1293 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329197 | 368616 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LF | CH54LF | ch5 4lf | ch54lf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1516 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 329057 | 368432 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LG | CH54LG | ch5 4lg | ch54lg | Flintshire | Sir Y Fflint | Connahs Quay STW | 1702 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328898 | 368334 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LH | CH54LH | ch5 4lh | ch54lh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1677 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328715 | 368683 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LJ | CH54LJ | ch5 4lj | ch54lj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1734 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328635 | 368724 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LL | CH54LL | ch5 4ll | ch54ll | Flintshire | Sir Y Fflint | Connahs Quay STW | 1332 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329018 | 368851 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LN | CH54LN | ch5 4ln | ch54ln | Flintshire | Sir Y Fflint | Connahs Quay STW | 1535 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328824 | 368789 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LP | CH54LP | ch5 4lp | ch54lp | Flintshire | Sir Y Fflint | Connahs Quay STW | 1395 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329109 | 368564 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LQ | CH54LQ | ch5 4lq | ch54lq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1860 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328793 | 368212 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LR | CH54LR | ch5 4lr | ch54lr | Flintshire | Sir Y Fflint | Connahs Quay STW | 1344 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329134 | 368617 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LS | CH54LS | ch5 4ls | ch54ls | Flintshire | Sir Y Fflint | Connahs Quay STW | 1379 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329086 | 368626 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LT | CH54LT | ch5 4lt | ch54lt | Flintshire | Sir Y Fflint | Connahs Quay STW | 1309 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329118 | 368706 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LU | CH54LU | ch5 4lu | ch54lu | Flintshire | Sir Y Fflint | Connahs Quay STW | 1298 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329110 | 368743 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LW | CH54LW | ch5 4lw | ch54lw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1658 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328679 | 368822 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LX | CH54LX | ch5 4lx | ch54lx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1122 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329294 | 368778 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LY | CH54LY | ch5 4ly | ch54ly | Flintshire | Sir Y Fflint | Connahs Quay STW | 1084 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329341 | 368775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4LZ | CH54LZ | ch5 4lz | ch54lz | Flintshire | Sir Y Fflint | Connahs Quay STW | 1846 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328521 | 368708 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NA | CH54NA | ch5 4na | ch54na | Flintshire | Sir Y Fflint | Connahs Quay STW | 1667 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328696 | 368752 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NB | CH54NB | ch5 4nb | ch54nb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1941 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328738 | 368152 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4ND | CH54ND | ch5 4nd | ch54nd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1972 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328786 | 368049 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NE | CH54NE | ch5 4ne | ch54ne | Flintshire | Sir Y Fflint | Connahs Quay STW | 2031 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328623 | 368153 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NF | CH54NF | ch5 4nf | ch54nf | Flintshire | Sir Y Fflint | Connahs Quay STW | 2097 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328702 | 367955 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NG | CH54NG | ch5 4ng | ch54ng | Flintshire | Sir Y Fflint | Connahs Quay STW | 2040 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328689 | 368056 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NH | CH54NH | ch5 4nh | ch54nh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1808 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328579 | 368667 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NJ | CH54NJ | ch5 4nj | ch54nj | Flintshire | Sir Y Fflint | Connahs Quay STW | 2210 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328385 | 368180 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NL | CH54NL | ch5 4nl | ch54nl | Flintshire | Sir Y Fflint | Connahs Quay STW | 349 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329902 | 369293 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NN | CH54NN | ch5 4nn | ch54nn | Flintshire | Sir Y Fflint | Connahs Quay STW | 643 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330006 | 368781 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NP | CH54NP | ch5 4np | ch54np | Flintshire | Sir Y Fflint | Connahs Quay STW | 438 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329806 | 369320 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NQ | CH54NQ | ch5 4nq | ch54nq | Flintshire | Sir Y Fflint | Connahs Quay STW | 2028 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328757 | 367997 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NR | CH54NR | ch5 4nr | ch54nr | Flintshire | Sir Y Fflint | Connahs Quay STW | 609 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329633 | 369423 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NS | CH54NS | ch5 4ns | ch54ns | Flintshire | Sir Y Fflint | Connahs Quay STW | 731 | 727 | 700to900 | 1.45 | 1.06 | 0.78 | 13.55 | 7.22 | 7.98 | 329524 | 369525 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NT | CH54NT | ch5 4nt | ch54nt | Flintshire | Sir Y Fflint | Connahs Quay STW | 589 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329651 | 369371 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NU | CH54NU | ch5 4nu | ch54nu | Flintshire | Sir Y Fflint | Connahs Quay STW | 407 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329863 | 369226 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NW | CH54NW | ch5 4nw | ch54nw | Flintshire | Sir Y Fflint | Connahs Quay STW | 406 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329836 | 369341 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NX | CH54NX | ch5 4nx | ch54nx | Flintshire | Sir Y Fflint | Connahs Quay STW | 313 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329962 | 369236 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NY | CH54NY | ch5 4ny | ch54ny | Flintshire | Sir Y Fflint | Connahs Quay STW | 544 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329795 | 369067 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4NZ | CH54NZ | ch5 4nz | ch54nz | Flintshire | Sir Y Fflint | Connahs Quay STW | 493 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329846 | 369084 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PA | CH54PA | ch5 4pa | ch54pa | Flintshire | Sir Y Fflint | Connahs Quay STW | 848 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329594 | 368831 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PB | CH54PB | ch5 4pb | ch54pb | Flintshire | Sir Y Fflint | Connahs Quay STW | 834 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329633 | 368808 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PD | CH54PD | ch5 4pd | ch54pd | Flintshire | Sir Y Fflint | Connahs Quay STW | 813 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329560 | 368934 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PE | CH54PE | ch5 4pe | ch54pe | Flintshire | Sir Y Fflint | Connahs Quay STW | 819 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329567 | 368913 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PF | CH54PF | ch5 4pf | ch54pf | Flintshire | Sir Y Fflint | Connahs Quay STW | 731 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329631 | 368977 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PG | CH54PG | ch5 4pg | ch54pg | Flintshire | Sir Y Fflint | Connahs Quay STW | 889 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329484 | 368913 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PH | CH54PH | ch5 4ph | ch54ph | Flintshire | Sir Y Fflint | Connahs Quay STW | 490 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329875 | 369054 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PJ | CH54PJ | ch5 4pj | ch54pj | Flintshire | Sir Y Fflint | Connahs Quay STW | 462 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329916 | 369051 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PL | CH54PL | ch5 4pl | ch54pl | Flintshire | Sir Y Fflint | Connahs Quay STW | 508 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329733 | 369409 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PN | CH54PN | ch5 4pn | ch54pn | Flintshire | Sir Y Fflint | Connahs Quay STW | 1049 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329250 | 369726 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PP | CH54PP | ch5 4pp | ch54pp | Flintshire | Sir Y Fflint | Connahs Quay STW | 2232 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328390 | 368132 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PQ | CH54PQ | ch5 4pq | ch54pq | Flintshire | Sir Y Fflint | Connahs Quay STW | 298 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329994 | 369212 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PR | CH54PR | ch5 4pr | ch54pr | Flintshire | Sir Y Fflint | Connahs Quay STW | 2175 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328453 | 368141 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PS | CH54PS | ch5 4ps | ch54ps | Flintshire | Sir Y Fflint | Connahs Quay STW | 2204 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328345 | 368257 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PT | CH54PT | ch5 4pt | ch54pt | Flintshire | Sir Y Fflint | Connahs Quay STW | 2016 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328333 | 368727 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PU | CH54PU | ch5 4pu | ch54pu | Flintshire | Sir Y Fflint | Connahs Quay STW | 2390 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328404 | 367851 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PW | CH54PW | ch5 4pw | ch54pw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1990 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328376 | 368684 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PX | CH54PX | ch5 4px | ch54px | Flintshire | Sir Y Fflint | Connahs Quay STW | 2019 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328562 | 368258 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PY | CH54PY | ch5 4py | ch54py | Flintshire | Sir Y Fflint | Connahs Quay STW | 2127 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328511 | 368143 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4PZ | CH54PZ | ch5 4pz | ch54pz | Flintshire | Sir Y Fflint | Connahs Quay STW | 2274 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328282 | 368225 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QA | CH54QA | ch5 4qa | ch54qa | Flintshire | Sir Y Fflint | Connahs Quay STW | 750 | 727 | 700to900 | 1.45 | 1.06 | 0.78 | 13.55 | 7.22 | 7.98 | 329526 | 369610 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TH | CH54TH | ch5 4th | ch54th | Flintshire | Sir Y Fflint | Connahs Quay STW | 1651 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328663 | 368892 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TJ | CH54TJ | ch5 4tj | ch54tj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1482 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328784 | 369105 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TL | CH54TL | ch5 4tl | ch54tl | Flintshire | Sir Y Fflint | Connahs Quay STW | 1533 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328751 | 369017 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TN | CH54TN | ch5 4tn | ch54tn | Flintshire | Sir Y Fflint | Connahs Quay STW | 1472 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328777 | 369218 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QB | CH54QB | ch5 4qb | ch54qb | Flintshire | Sir Y Fflint | Connahs Quay STW | 777 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329476 | 369522 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QD | CH54QD | ch5 4qd | ch54qd | Flintshire | Sir Y Fflint | Connahs Quay STW | 778 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329465 | 369443 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QE | CH54QE | ch5 4qe | ch54qe | Flintshire | Sir Y Fflint | Connahs Quay STW | 806 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329436 | 369430 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QF | CH54QF | ch5 4qf | ch54qf | Flintshire | Sir Y Fflint | Connahs Quay STW | 774 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329467 | 369353 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QG | CH54QG | ch5 4qg | ch54qg | Flintshire | Sir Y Fflint | Connahs Quay STW | 734 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329509 | 369444 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QH | CH54QH | ch5 4qh | ch54qh | Flintshire | Sir Y Fflint | Connahs Quay STW | 589 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329655 | 369312 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QJ | CH54QJ | ch5 4qj | ch54qj | Flintshire | Sir Y Fflint | Connahs Quay STW | 514 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329732 | 369302 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QL | CH54QL | ch5 4ql | ch54ql | Flintshire | Sir Y Fflint | Connahs Quay STW | 581 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329717 | 369127 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QN | CH54QN | ch5 4qn | ch54qn | Flintshire | Sir Y Fflint | Connahs Quay STW | 521 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329747 | 369213 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QP | CH54QP | ch5 4qp | ch54qp | Flintshire | Sir Y Fflint | Connahs Quay STW | 986 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329304 | 369072 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QQ | CH54QQ | ch5 4qq | ch54qq | Flintshire | Sir Y Fflint | Connahs Quay STW | 635 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329614 | 369272 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QR | CH54QR | ch5 4qr | ch54qr | Flintshire | Sir Y Fflint | Connahs Quay STW | 2204 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328171 | 368624 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QS | CH54QS | ch5 4qs | ch54qs | Flintshire | Sir Y Fflint | Connahs Quay STW | 2472 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328174 | 368025 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QT | CH54QT | ch5 4qt | ch54qt | Flintshire | Sir Y Fflint | Connahs Quay STW | 2303 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328518 | 367852 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QU | CH54QU | ch5 4qu | ch54qu | Flintshire | Sir Y Fflint | Connahs Quay STW | 1986 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328258 | 369271 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QW | CH54QW | ch5 4qw | ch54qw | Flintshire | Sir Y Fflint | Connahs Quay STW | 974 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329335 | 369022 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QX | CH54QX | ch5 4qx | ch54qx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1689 | 764 | 700to900 | 1.53 | 1.12 | 0.82 | 14.24 | 7.59 | 8.39 | 328945 | 368296 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QY | CH54QY | ch5 4qy | ch54qy | Flintshire | Sir Y Fflint | Connahs Quay STW | 2134 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328256 | 368595 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4QZ | CH54QZ | ch5 4qz | ch54qz | Flintshire | Sir Y Fflint | Connahs Quay STW | 2447 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328334 | 367847 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RA | CH54RA | ch5 4ra | ch54ra | Flintshire | Sir Y Fflint | Connahs Quay STW | 627 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329634 | 369221 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RB | CH54RB | ch5 4rb | ch54rb | Flintshire | Sir Y Fflint | Connahs Quay STW | 711 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 329574 | 369131 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RD | CH54RD | ch5 4rd | ch54rd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1005 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329268 | 369126 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RE | CH54RE | ch5 4re | ch54re | Flintshire | Sir Y Fflint | Connahs Quay STW | 1011 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329361 | 368881 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RF | CH54RF | ch5 4rf | ch54rf | Flintshire | Sir Y Fflint | Connahs Quay STW | 941 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329382 | 368995 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RG | CH54RG | ch5 4rg | ch54rg | Flintshire | Sir Y Fflint | Connahs Quay STW | 910 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329432 | 368961 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RH | CH54RH | ch5 4rh | ch54rh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1974 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328272 | 369235 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RJ | CH54RJ | ch5 4rj | ch54rj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1840 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328401 | 369350 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RL | CH54RL | ch5 4rl | ch54rl | Flintshire | Sir Y Fflint | Connahs Quay STW | 1931 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328310 | 369359 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RN | CH54RN | ch5 4rn | ch54rn | Flintshire | Sir Y Fflint | Connahs Quay STW | 1926 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328324 | 369566 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RP | CH54RP | ch5 4rp | ch54rp | Flintshire | Sir Y Fflint | Connahs Quay STW | 2011 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328241 | 369596 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RQ | CH54RQ | ch5 4rq | ch54rq | Flintshire | Sir Y Fflint | Connahs Quay STW | 949 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329345 | 369695 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RR | CH54RR | ch5 4rr | ch54rr | Flintshire | Sir Y Fflint | Connahs Quay STW | 2126 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328178 | 368864 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RS | CH54RS | ch5 4rs | ch54rs | Flintshire | Sir Y Fflint | Connahs Quay STW | 1964 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328341 | 368880 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RT | CH54RT | ch5 4rt | ch54rt | Flintshire | Sir Y Fflint | Connahs Quay STW | 1986 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328262 | 369207 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RU | CH54RU | ch5 4ru | ch54ru | Flintshire | Sir Y Fflint | Connahs Quay STW | 2303 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328345 | 368073 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RW | CH54RW | ch5 4rw | ch54rw | Flintshire | Sir Y Fflint | Connahs Quay STW | 2036 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328221 | 369123 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RX | CH54RX | ch5 4rx | ch54rx | Flintshire | Sir Y Fflint | Connahs Quay STW | 2283 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328387 | 368047 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RY | CH54RY | ch5 4ry | ch54ry | Flintshire | Sir Y Fflint | Connahs Quay STW | 2323 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328383 | 367986 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4RZ | CH54RZ | ch5 4rz | ch54rz | Flintshire | Sir Y Fflint | Connahs Quay STW | 2338 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328398 | 367941 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SA | CH54SA | ch5 4sa | ch54sa | Flintshire | Sir Y Fflint | Connahs Quay STW | 845 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329414 | 369557 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SB | CH54SB | ch5 4sb | ch54sb | Flintshire | Sir Y Fflint | Connahs Quay STW | 806 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329476 | 369635 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SD | CH54SD | ch5 4sd | ch54sd | Flintshire | Sir Y Fflint | Connahs Quay STW | 2200 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328120 | 368796 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SE | CH54SE | ch5 4se | ch54se | Flintshire | Sir Y Fflint | Connahs Quay STW | 1277 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328964 | 369363 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SF | CH54SF | ch5 4sf | ch54sf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1327 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328917 | 369289 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SG | CH54SG | ch5 4sg | ch54sg | Flintshire | Sir Y Fflint | Connahs Quay STW | 833 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329408 | 369418 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SH | CH54SH | ch5 4sh | ch54sh | Flintshire | Sir Y Fflint | Connahs Quay STW | 2058 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328235 | 368920 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SJ | CH54SJ | ch5 4sj | ch54sj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1060 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329197 | 369193 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SL | CH54SL | ch5 4sl | ch54sl | Flintshire | Sir Y Fflint | Connahs Quay STW | 1164 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329087 | 369221 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SN | CH54SN | ch5 4sn | ch54sn | Flintshire | Sir Y Fflint | Connahs Quay STW | 1218 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329023 | 369398 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SP | CH54SP | ch5 4sp | ch54sp | Flintshire | Sir Y Fflint | Connahs Quay STW | 1075 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329166 | 369407 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SQ | CH54SQ | ch5 4sq | ch54sq | Flintshire | Sir Y Fflint | Connahs Quay STW | 922 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329318 | 369375 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SR | CH54SR | ch5 4sr | ch54sr | Flintshire | Sir Y Fflint | Connahs Quay STW | 1131 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329110 | 369398 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SS | CH54SS | ch5 4ss | ch54ss | Flintshire | Sir Y Fflint | Connahs Quay STW | 1094 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329147 | 369346 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4ST | CH54ST | ch5 4st | ch54st | Flintshire | Sir Y Fflint | Connahs Quay STW | 1331 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328910 | 369425 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SU | CH54SU | ch5 4su | ch54su | Flintshire | Sir Y Fflint | Connahs Quay STW | 1456 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328789 | 369496 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SW | CH54SW | ch5 4sw | ch54sw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1309 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328932 | 369420 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SX | CH54SX | ch5 4sx | ch54sx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1322 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328920 | 369316 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SY | CH54SY | ch5 4sy | ch54sy | Flintshire | Sir Y Fflint | Connahs Quay STW | 1169 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329102 | 369113 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4SZ | CH54SZ | ch5 4sz | ch54sz | Flintshire | Sir Y Fflint | Connahs Quay STW | 1225 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329021 | 369265 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TA | CH54TA | ch5 4ta | ch54ta | Flintshire | Sir Y Fflint | Connahs Quay STW | 1414 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328859 | 369079 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TB | CH54TB | ch5 4tb | ch54tb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1432 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328834 | 369110 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TD | CH54TD | ch5 4td | ch54td | Flintshire | Sir Y Fflint | Connahs Quay STW | 1378 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328898 | 369070 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TE | CH54TE | ch5 4te | ch54te | Flintshire | Sir Y Fflint | Connahs Quay STW | 1383 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328905 | 369021 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TF | CH54TF | ch5 4tf | ch54tf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1282 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329016 | 369001 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TG | CH54TG | ch5 4tg | ch54tg | Flintshire | Sir Y Fflint | Connahs Quay STW | 1372 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328929 | 368977 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TP | CH54TP | ch5 4tp | ch54tp | Flintshire | Sir Y Fflint | Connahs Quay STW | 1594 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328685 | 369033 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TQ | CH54TQ | ch5 4tq | ch54tq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1421 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328879 | 368974 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TR | CH54TR | ch5 4tr | ch54tr | Flintshire | Sir Y Fflint | Connahs Quay STW | 1255 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328989 | 369283 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TS | CH54TS | ch5 4ts | ch54ts | Flintshire | Sir Y Fflint | Connahs Quay STW | 1280 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328961 | 369361 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TT | CH54TT | ch5 4tt | ch54tt | Flintshire | Sir Y Fflint | Connahs Quay STW | 1655 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328627 | 369014 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TU | CH54TU | ch5 4tu | ch54tu | Flintshire | Sir Y Fflint | Connahs Quay STW | 1660 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328646 | 368918 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TW | CH54TW | ch5 4tw | ch54tw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1497 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328757 | 369183 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TX | CH54TX | ch5 4tx | ch54tx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1708 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328558 | 369086 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TY | CH54TY | ch5 4ty | ch54ty | Flintshire | Sir Y Fflint | Connahs Quay STW | 1802 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328474 | 369023 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4TZ | CH54TZ | ch5 4tz | ch54tz | Flintshire | Sir Y Fflint | Connahs Quay STW | 1719 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328572 | 368967 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UA | CH54UA | ch5 4ua | ch54ua | Flintshire | Sir Y Fflint | Connahs Quay STW | 1766 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328526 | 368956 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UB | CH54UB | ch5 4ub | ch54ub | Flintshire | Sir Y Fflint | Connahs Quay STW | 1775 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328524 | 368928 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UD | CH54UD | ch5 4ud | ch54ud | Flintshire | Sir Y Fflint | Connahs Quay STW | 1739 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328508 | 369231 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UE | CH54UE | ch5 4ue | ch54ue | Flintshire | Sir Y Fflint | Connahs Quay STW | 1797 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328457 | 369163 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UF | CH54UF | ch5 4uf | ch54uf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1852 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328441 | 368941 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UG | CH54UG | ch5 4ug | ch54ug | Flintshire | Sir Y Fflint | Connahs Quay STW | 1912 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328395 | 368881 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UH | CH54UH | ch5 4uh | ch54uh | Flintshire | Sir Y Fflint | Connahs Quay STW | 866 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329375 | 369335 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UJ | CH54UJ | ch5 4uj | ch54uj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1854 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328472 | 368824 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UL | CH54UL | ch5 4ul | ch54ul | Flintshire | Sir Y Fflint | Connahs Quay STW | 1849 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328459 | 368884 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UN | CH54UN | ch5 4un | ch54un | Flintshire | Sir Y Fflint | Connahs Quay STW | 2250 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328152 | 368545 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UQ | CH54UQ | ch5 4uq | ch54uq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1899 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328375 | 369025 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UR | CH54UR | ch5 4ur | ch54ur | Flintshire | Sir Y Fflint | Connahs Quay STW | 1504 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328874 | 370008 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4US | CH54US | ch5 4us | ch54us | Flintshire | Sir Y Fflint | Connahs Quay STW | 1391 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328938 | 369868 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UT | CH54UT | ch5 4ut | ch54ut | Flintshire | Sir Y Fflint | Connahs Quay STW | 1446 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328834 | 369717 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UU | CH54UU | ch5 4uu | ch54uu | Flintshire | Sir Y Fflint | Connahs Quay STW | 1448 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328849 | 369779 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UW | CH54UW | ch5 4uw | ch54uw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1374 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328972 | 369908 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UX | CH54UX | ch5 4ux | ch54ux | Flintshire | Sir Y Fflint | Connahs Quay STW | 1460 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328871 | 369886 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UY | CH54UY | ch5 4uy | ch54uy | Flintshire | Sir Y Fflint | Connahs Quay STW | 1487 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328840 | 369880 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4UZ | CH54UZ | ch5 4uz | ch54uz | Flintshire | Sir Y Fflint | Connahs Quay STW | 1583 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328717 | 369810 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WA | CH54WA | ch5 4wa | ch54wa | Flintshire | Sir Y Fflint | Connahs Quay STW | 1394 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328856 | 369543 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WB | CH54WB | ch5 4wb | ch54wb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1599 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328643 | 369457 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WD | CH54WD | ch5 4wd | ch54wd | Flintshire | Sir Y Fflint | Connahs Quay STW | 2110 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328193 | 369890 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WE | CH54WE | ch5 4we | ch54we | Flintshire | Sir Y Fflint | Connahs Quay STW | 2067 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328225 | 369838 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WF | CH54WF | ch5 4wf | ch54wf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1971 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328306 | 369758 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WG | CH54WG | ch5 4wg | ch54wg | Flintshire | Sir Y Fflint | Connahs Quay STW | 1588 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328653 | 369371 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WH | CH54WH | ch5 4wh | ch54wh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1957 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328309 | 369696 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WJ | CH54WJ | ch5 4wj | ch54wj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1906 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328352 | 369640 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WL | CH54WL | ch5 4wl | ch54wl | Flintshire | Sir Y Fflint | Connahs Quay STW | 1959 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328300 | 369109 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WN | CH54WN | ch5 4wn | ch54wn | Flintshire | Sir Y Fflint | Connahs Quay STW | 129 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 330132 | 369309 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WP | CH54WP | ch5 4wp | ch54wp | Flintshire | Sir Y Fflint | Connahs Quay STW | 2100 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328177 | 369766 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WQ | CH54WQ | ch5 4wq | ch54wq | Flintshire | Sir Y Fflint | Connahs Quay STW | 2047 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328224 | 369729 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WR | CH54WR | ch5 4wr | ch54wr | Flintshire | Sir Y Fflint | Connahs Quay STW | 874 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 329417 | 369674 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WX | CH54WX | ch5 4wx | ch54wx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1988 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328295 | 368972 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WY | CH54WY | ch5 4wy | ch54wy | Flintshire | Sir Y Fflint | Connahs Quay STW | 2001 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328240 | 369348 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4WZ | CH54WZ | ch5 4wz | ch54wz | Flintshire | Sir Y Fflint | Connahs Quay STW | 2007 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328234 | 369419 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XA | CH54XA | ch5 4xa | ch54xa | Flintshire | Sir Y Fflint | Connahs Quay STW | 1621 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328694 | 369865 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XB | CH54XB | ch5 4xb | ch54xb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1542 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328809 | 369953 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XD | CH54XD | ch5 4xd | ch54xd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1773 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328630 | 370121 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XE | CH54XE | ch5 4xe | ch54xe | Flintshire | Sir Y Fflint | Connahs Quay STW | 1626 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328727 | 369974 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XF | CH54XF | ch5 4xf | ch54xf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1613 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328781 | 370066 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XG | CH54XG | ch5 4xg | ch54xg | Flintshire | Sir Y Fflint | Connahs Quay STW | 1455 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328865 | 369855 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XH | CH54XH | ch5 4xh | ch54xh | Flintshire | Sir Y Fflint | Connahs Quay STW | 1610 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328646 | 369602 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XJ | CH54XJ | ch5 4xj | ch54xj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1523 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328718 | 369429 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XL | CH54XL | ch5 4xl | ch54xl | Flintshire | Sir Y Fflint | Connahs Quay STW | 1514 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328727 | 369344 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XN | CH54XN | ch5 4xn | ch54xn | Flintshire | Sir Y Fflint | Connahs Quay STW | 1437 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328812 | 369223 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XP | CH54XP | ch5 4xp | ch54xp | Flintshire | Sir Y Fflint | Connahs Quay STW | 1236 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329037 | 369096 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XQ | CH54XQ | ch5 4xq | ch54xq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1637 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328613 | 369552 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XR | CH54XR | ch5 4xr | ch54xr | Flintshire | Sir Y Fflint | Connahs Quay STW | 1226 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 329050 | 369086 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XS | CH54XS | ch5 4xs | ch54xs | Flintshire | Sir Y Fflint | Connahs Quay STW | 1704 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328646 | 369980 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XT | CH54XT | ch5 4xt | ch54xt | Flintshire | Sir Y Fflint | Connahs Quay STW | 1789 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328566 | 370008 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XU | CH54XU | ch5 4xu | ch54xu | Flintshire | Sir Y Fflint | Connahs Quay STW | 1799 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328570 | 370046 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XW | CH54XW | ch5 4xw | ch54xw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1395 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 328848 | 369291 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XX | CH54XX | ch5 4xx | ch54xx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1691 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328688 | 370050 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4XY | CH54XY | ch5 4xy | ch54xy | Flintshire | Sir Y Fflint | Connahs Quay STW | 1705 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328687 | 370083 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YA | CH54YA | ch5 4ya | ch54ya | Flintshire | Sir Y Fflint | Connahs Quay STW | 1777 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328464 | 369360 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YB | CH54YB | ch5 4yb | ch54yb | Flintshire | Sir Y Fflint | Connahs Quay STW | 1781 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328462 | 369288 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YD | CH54YD | ch5 4yd | ch54yd | Flintshire | Sir Y Fflint | Connahs Quay STW | 1799 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328448 | 369233 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YE | CH54YE | ch5 4ye | ch54ye | Flintshire | Sir Y Fflint | Connahs Quay STW | 1798 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328540 | 369965 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YF | CH54YF | ch5 4yf | ch54yf | Flintshire | Sir Y Fflint | Connahs Quay STW | 1945 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328467 | 370178 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YG | CH54YG | ch5 4yg | ch54yg | Flintshire | Sir Y Fflint | Connahs Quay STW | 1871 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328377 | 369544 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YH | CH54YH | ch5 4yh | ch54yh | Flintshire | Sir Y Fflint | Connahs Quay STW | 2032 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328209 | 369412 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YJ | CH54YJ | ch5 4yj | ch54yj | Flintshire | Sir Y Fflint | Connahs Quay STW | 1932 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 328324 | 369622 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YL | CH54YL | ch5 4yl | ch54yl | Flintshire | Sir Y Fflint | Connahs Quay STW | 1832 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328410 | 369442 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YP | CH54YP | ch5 4yp | ch54yp | Flintshire | Sir Y Fflint | Connahs Quay STW | 1402 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328969 | 369970 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YQ | CH54YQ | ch5 4yq | ch54yq | Flintshire | Sir Y Fflint | Connahs Quay STW | 1915 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328327 | 369444 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YR | CH54YR | ch5 4yr | ch54yr | Flintshire | Sir Y Fflint | Connahs Quay STW | 1405 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328956 | 369949 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YS | CH54YS | ch5 4ys | ch54ys | Flintshire | Sir Y Fflint | Connahs Quay STW | 1398 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328946 | 369909 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YT | CH54YT | ch5 4yt | ch54yt | Flintshire | Sir Y Fflint | Connahs Quay STW | 1480 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328883 | 369970 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YU | CH54YU | ch5 4yu | ch54yu | Flintshire | Sir Y Fflint | Connahs Quay STW | 1466 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328919 | 370014 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YW | CH54YW | ch5 4yw | ch54yw | Flintshire | Sir Y Fflint | Connahs Quay STW | 1443 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328926 | 369975 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4YX | CH54YX | ch5 4yx | ch54yx | Flintshire | Sir Y Fflint | Connahs Quay STW | 1423 | 740 | 700to900 | 1.48 | 1.08 | 0.79 | 13.79 | 7.36 | 8.13 | 328952 | 369983 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4ZA | CH54ZA | ch5 4za | ch54za | Flintshire | Sir Y Fflint | Connahs Quay STW | 2424 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328246 | 368004 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4ZB | CH54ZB | ch5 4zb | ch54zb | Flintshire | Sir Y Fflint | Connahs Quay STW | 2363 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328225 | 368147 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4ZD | CH54ZD | ch5 4zd | ch54zd | Flintshire | Sir Y Fflint | Connahs Quay STW | 2389 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328179 | 368173 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4ZE | CH54ZE | ch5 4ze | ch54ze | Flintshire | Sir Y Fflint | Connahs Quay STW | 2338 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328187 | 368263 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 4ZS | CH54ZS | ch5 4zs | ch54zs | Flintshire | Sir Y Fflint | Connahs Quay STW | 2384 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 328246 | 368074 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 9AN | CH59AN | ch5 9an | ch59an | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 9BW | CH59BW | ch5 9bw | ch59bw | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 9EH | CH59EH | ch5 9eh | ch59eh | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 9EP | CH59EP | ch5 9ep | ch59ep | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 9ES | CH59ES | ch5 9es | ch59es | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 9EU | CH59EU | ch5 9eu | ch59eu | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 9EY | CH59EY | ch5 9ey | ch59ey | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 9FJ | CH59FJ | ch5 9fj | ch59fj | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 9FL | CH59FL | ch5 9fl | ch59fl | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 9FN | CH59FN | ch5 9fn | ch59fn | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 9FQ | CH59FQ | ch5 9fq | ch59fq | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH5 9FR | CH59FR | ch5 9fr | ch59fr | Flintshire | Sir Y Fflint | Queensferry WwTW | 233 | 723 | 700to900 | 1.45 | 1.06 | 0.78 | 13.47 | 7.18 | 7.94 | 332162 | 368438 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH6 5GX | CH65GX | ch6 5gx | ch65gx | Flintshire | Sir Y Fflint | Connahs Quay STW | 2807 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 327749 | 370671 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH6 5SJ | CH65SJ | ch6 5sj | ch65sj | Flintshire | Sir Y Fflint | Connahs Quay STW | 3466 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 327259 | 371146 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TE | CH65TE | ch6 5te | ch65te | Flintshire | Sir Y Fflint | Connahs Quay STW | 3590 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 327115 | 371144 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TF | CH65TF | ch6 5tf | ch65tf | Flintshire | Sir Y Fflint | Connahs Quay STW | 2984 | 759 | 700to900 | 1.52 | 1.11 | 0.82 | 14.15 | 7.55 | 8.34 | 327334 | 370054 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH6 5TH | CH65TH | ch6 5th | ch65th | Flintshire | Sir Y Fflint | Connahs Quay STW | 3020 | 745 | 700to900 | 1.49 | 1.09 | 0.8 | 13.89 | 7.41 | 8.19 | 327571 | 370790 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AA | CH71AA | ch7 1aa | ch71aa | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AB | CH71AB | ch7 1ab | ch71ab | Flintshire | Sir Y Fflint | Mold WwTW | 1363 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323672 | 363973 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AD | CH71AD | ch7 1ad | ch71ad | Flintshire | Sir Y Fflint | Mold WwTW | 1357 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323748 | 364054 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AE | CH71AE | ch7 1ae | ch71ae | Flintshire | Sir Y Fflint | Mold WwTW | 2007 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324093 | 365036 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AF | CH71AF | ch7 1af | ch71af | Flintshire | Sir Y Fflint | Mold WwTW | 1206 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323650 | 363633 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AG | CH71AG | ch7 1ag | ch71ag | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AJ | CH71AJ | ch7 1aj | ch71aj | Flintshire | Sir Y Fflint | Mold WwTW | 1370 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323687 | 364003 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AL | CH71AL | ch7 1al | ch71al | Flintshire | Sir Y Fflint | Mold WwTW | 1377 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323668 | 363991 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AN | CH71AN | ch7 1an | ch71an | Flintshire | Sir Y Fflint | Mold WwTW | 1369 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323688 | 364003 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AP | CH71AP | ch7 1ap | ch71ap | Flintshire | Sir Y Fflint | Mold WwTW | 1322 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323668 | 363899 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AR | CH71AR | ch7 1ar | ch71ar | Flintshire | Sir Y Fflint | Mold WwTW | 1305 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323740 | 363966 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AS | CH71AS | ch7 1as | ch71as | Flintshire | Sir Y Fflint | Mold WwTW | 1239 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323767 | 363894 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AX | CH71AX | ch7 1ax | ch71ax | Flintshire | Sir Y Fflint | Mold WwTW | 1404 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323608 | 363956 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1AZ | CH71AZ | ch7 1az | ch71az | Flintshire | Sir Y Fflint | Mold WwTW | 1291 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323745 | 363950 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BA | CH71BA | ch7 1ba | ch71ba | Flintshire | Sir Y Fflint | Mold WwTW | 1422 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323678 | 364073 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BB | CH71BB | ch7 1bb | ch71bb | Flintshire | Sir Y Fflint | Mold WwTW | 1403 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323689 | 364058 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BE | CH71BE | ch7 1be | ch71be | Flintshire | Sir Y Fflint | Mold WwTW | 1464 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323654 | 364110 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BF | CH71BF | ch7 1bf | ch71bf | Flintshire | Sir Y Fflint | Mold WwTW | 2168 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323337 | 364784 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BG | CH71BG | ch7 1bg | ch71bg | Flintshire | Sir Y Fflint | Mold WwTW | 1574 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323763 | 364366 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BH | CH71BH | ch7 1bh | ch71bh | Flintshire | Sir Y Fflint | Mold WwTW | 1475 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323645 | 364117 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BL | CH71BL | ch7 1bl | ch71bl | Flintshire | Sir Y Fflint | Mold WwTW | 1742 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323566 | 364417 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BN | CH71BN | ch7 1bn | ch71bn | Flintshire | Sir Y Fflint | Mold WwTW | 1456 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323617 | 364054 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BP | CH71BP | ch7 1bp | ch71bp | Flintshire | Sir Y Fflint | Mold WwTW | 2148 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323304 | 364727 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BQ | CH71BQ | ch7 1bq | ch71bq | Flintshire | Sir Y Fflint | Mold WwTW | 1423 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323697 | 364096 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BT | CH71BT | ch7 1bt | ch71bt | Flintshire | Sir Y Fflint | Mold WwTW | 2290 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323264 | 364881 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BU | CH71BU | ch7 1bu | ch71bu | Flintshire | Sir Y Fflint | Mold WwTW | 1838 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 323551 | 364532 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BW | CH71BW | ch7 1bw | ch71bw | Flintshire | Sir Y Fflint | Mold WwTW | 1421 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323721 | 364119 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BX | CH71BX | ch7 1bx | ch71bx | Flintshire | Sir Y Fflint | Mold WwTW | 1907 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 323519 | 364595 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1BY | CH71BY | ch7 1by | ch71by | Flintshire | Sir Y Fflint | Mold WwTW | 1909 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 323503 | 364584 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DA | CH71DA | ch7 1da | ch71da | Flintshire | Sir Y Fflint | Mold WwTW | 2073 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323395 | 364708 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DB | CH71DB | ch7 1db | ch71db | Flintshire | Sir Y Fflint | Mold WwTW | 1318 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323753 | 364002 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DE | CH71DE | ch7 1de | ch71de | Flintshire | Sir Y Fflint | Mold WwTW | 1883 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323427 | 364479 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DF | CH71DF | ch7 1df | ch71df | Flintshire | Sir Y Fflint | Mold WwTW | 1931 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323398 | 364518 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DG | CH71DG | ch7 1dg | ch71dg | Flintshire | Sir Y Fflint | Mold WwTW | 1619 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323651 | 364328 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DH | CH71DH | ch7 1dh | ch71dh | Flintshire | Sir Y Fflint | Mold WwTW | 1620 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323761 | 364423 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DJ | CH71DJ | ch7 1dj | ch71dj | Flintshire | Sir Y Fflint | Mold WwTW | 1488 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323627 | 364116 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DN | CH71DN | ch7 1dn | ch71dn | Flintshire | Sir Y Fflint | Mold WwTW | 1464 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323552 | 363980 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DP | CH71DP | ch7 1dp | ch71dp | Flintshire | Sir Y Fflint | Mold WwTW | 1387 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323595 | 363908 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DQ | CH71DQ | ch7 1dq | ch71dq | Flintshire | Sir Y Fflint | Mold WwTW | 1370 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323697 | 364015 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DR | CH71DR | ch7 1dr | ch71dr | Flintshire | Sir Y Fflint | Mold WwTW | 1442 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323496 | 363850 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DS | CH71DS | ch7 1ds | ch71ds | Flintshire | Sir Y Fflint | Mold WwTW | 1331 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323634 | 363864 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DT | CH71DT | ch7 1dt | ch71dt | Flintshire | Sir Y Fflint | Mold WwTW | 1315 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323642 | 363847 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DW | CH71DW | ch7 1dw | ch71dw | Flintshire | Sir Y Fflint | Mold WwTW | 1453 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323548 | 363956 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DX | CH71DX | ch7 1dx | ch71dx | Flintshire | Sir Y Fflint | Mold WwTW | 1031 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324017 | 363864 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1DZ | CH71DZ | ch7 1dz | ch71dz | Flintshire | Sir Y Fflint | Mold WwTW | 1353 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323600 | 363852 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1EF | CH71EF | ch7 1ef | ch71ef | Flintshire | Sir Y Fflint | Mold WwTW | 1265 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323897 | 364074 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1EG | CH71EG | ch7 1eg | ch71eg | Flintshire | Sir Y Fflint | Mold WwTW | 1186 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323879 | 363944 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1EH | CH71EH | ch7 1eh | ch71eh | Flintshire | Sir Y Fflint | Mold WwTW | 1498 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323253 | 363194 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1EJ | CH71EJ | ch7 1ej | ch71ej | Flintshire | Sir Y Fflint | Mold WwTW | 1103 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323943 | 363891 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1EP | CH71EP | ch7 1ep | ch71ep | Flintshire | Sir Y Fflint | Mold WwTW | 937 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323822 | 363267 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1EQ | CH71EQ | ch7 1eq | ch71eq | Flintshire | Sir Y Fflint | Mold WwTW | 303 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324454 | 363074 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1ER | CH71ER | ch7 1er | ch71er | Flintshire | Sir Y Fflint | Mold WwTW | 1207 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323804 | 363889 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1ES | CH71ES | ch7 1es | ch71es | Flintshire | Sir Y Fflint | Mold WwTW | 1150 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323819 | 363814 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1ET | CH71ET | ch7 1et | ch71et | Flintshire | Sir Y Fflint | Mold WwTW | 1154 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323799 | 363793 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1EW | CH71EW | ch7 1ew | ch71ew | Flintshire | Sir Y Fflint | Mold WwTW | 1075 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323951 | 363858 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1EX | CH71EX | ch7 1ex | ch71ex | Flintshire | Sir Y Fflint | Mold WwTW | 353 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324397 | 363127 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1EZ | CH71EZ | ch7 1ez | ch71ez | Flintshire | Sir Y Fflint | Mold WwTW | 872 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323959 | 363506 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FA | CH71FA | ch7 1fa | ch71fa | Flintshire | Sir Y Fflint | Mold WwTW | 1669 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323088 | 362994 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FB | CH71FB | ch7 1fb | ch71fb | Flintshire | Sir Y Fflint | Mold WwTW | 706 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324108 | 362848 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FD | CH71FD | ch7 1fd | ch71fd | Flintshire | Sir Y Fflint | Mold WwTW | 758 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324066 | 362814 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FG | CH71FG | ch7 1fg | ch71fg | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FH | CH71FH | ch7 1fh | ch71fh | Flintshire | Sir Y Fflint | Mold WwTW | 1594 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324024 | 364559 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FJ | CH71FJ | ch7 1fj | ch71fj | Flintshire | Sir Y Fflint | Mold WwTW | 1374 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323390 | 362945 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FL | CH71FL | ch7 1fl | ch71fl | Flintshire | Sir Y Fflint | Mold WwTW | 1528 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323247 | 362870 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FN | CH71FN | ch7 1fn | ch71fn | Flintshire | Sir Y Fflint | Mold WwTW | 1445 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323328 | 362886 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FP | CH71FP | ch7 1fp | ch71fp | Flintshire | Sir Y Fflint | Mold WwTW | 1918 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 322837 | 363265 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FQ | CH71FQ | ch7 1fq | ch71fq | Flintshire | Sir Y Fflint | Mold WwTW | 730 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324058 | 362909 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FR | CH71FR | ch7 1fr | ch71fr | Flintshire | Sir Y Fflint | Mold WwTW | 811 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323987 | 362865 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FS | CH71FS | ch7 1fs | ch71fs | Flintshire | Sir Y Fflint | Mold WwTW | 736 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324038 | 362956 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FT | CH71FT | ch7 1ft | ch71ft | Flintshire | Sir Y Fflint | Mold WwTW | 1795 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 323633 | 364544 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FW | CH71FW | ch7 1fw | ch71fw | Flintshire | Sir Y Fflint | Mold WwTW | 970 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323902 | 363611 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FX | CH71FX | ch7 1fx | ch71fx | Flintshire | Sir Y Fflint | Mold WwTW | 1381 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323390 | 362905 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FY | CH71FY | ch7 1fy | ch71fy | Flintshire | Sir Y Fflint | Mold WwTW | 1181 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323596 | 362890 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1FZ | CH71FZ | ch7 1fz | ch71fz | Flintshire | Sir Y Fflint | Mold WwTW | 1615 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323149 | 362930 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GA | CH71GA | ch7 1ga | ch71ga | Flintshire | Sir Y Fflint | Mold WwTW | 1082 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323857 | 363750 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GB | CH71GB | ch7 1gb | ch71gb | Flintshire | Sir Y Fflint | Mold WwTW | 1609 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323142 | 363184 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GD | CH71GD | ch7 1gd | ch71gd | Flintshire | Sir Y Fflint | Mold WwTW | 1622 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323348 | 363955 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GE | CH71GE | ch7 1ge | ch71ge | Flintshire | Sir Y Fflint | Mold WwTW | 2070 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322826 | 363902 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GF | CH71GF | ch7 1gf | ch71gf | Flintshire | Sir Y Fflint | Mold WwTW | 2053 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322854 | 363926 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GG | CH71GG | ch7 1gg | ch71gg | Flintshire | Sir Y Fflint | Mold WwTW | 2039 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322891 | 363977 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GH | CH71GH | ch7 1gh | ch71gh | Flintshire | Sir Y Fflint | Mold WwTW | 1637 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323120 | 363285 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GJ | CH71GJ | ch7 1gj | ch71gj | Flintshire | Sir Y Fflint | Mold WwTW | 1681 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323356 | 364078 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GL | CH71GL | ch7 1gl | ch71gl | Flintshire | Sir Y Fflint | Mold WwTW | 654 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324136 | 363366 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GN | CH71GN | ch7 1gn | ch71gn | Flintshire | Sir Y Fflint | Mold WwTW | 1515 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323602 | 364128 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GP | CH71GP | ch7 1gp | ch71gp | Flintshire | Sir Y Fflint | Mold WwTW | 1532 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323843 | 364374 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GQ | CH71GQ | ch7 1gq | ch71gq | Flintshire | Sir Y Fflint | Mold WwTW | 1703 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323057 | 363316 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GR | CH71GR | ch7 1gr | ch71gr | Flintshire | Sir Y Fflint | Mold WwTW | 1726 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323027 | 363236 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GS | CH71GS | ch7 1gs | ch71gs | Flintshire | Sir Y Fflint | Mold WwTW | 566 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324334 | 363523 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GT | CH71GT | ch7 1gt | ch71gt | Flintshire | Sir Y Fflint | Mold WwTW | 729 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324248 | 363668 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GU | CH71GU | ch7 1gu | ch71gu | Flintshire | Sir Y Fflint | Mold WwTW | 1921 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 322831 | 363203 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GW | CH71GW | ch7 1gw | ch71gw | Flintshire | Sir Y Fflint | Mold WwTW | 1812 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 322952 | 363357 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GX | CH71GX | ch7 1gx | ch71gx | Flintshire | Sir Y Fflint | Mold WwTW | 1799 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 322952 | 363095 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GY | CH71GY | ch7 1gy | ch71gy | Flintshire | Sir Y Fflint | Mold WwTW | 1883 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 322870 | 363237 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1GZ | CH71GZ | ch7 1gz | ch71gz | Flintshire | Sir Y Fflint | Mold WwTW | 1783 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 322974 | 363294 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HA | CH71HA | ch7 1ha | ch71ha | Flintshire | Sir Y Fflint | Mold WwTW | 382 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324433 | 363353 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HE | CH71HE | ch7 1he | ch71he | Flintshire | Sir Y Fflint | Mold WwTW | 163 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 324664 | 363002 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HF | CH71HF | ch7 1hf | ch71hf | Flintshire | Sir Y Fflint | Mold WwTW | 521 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324376 | 363503 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HH | CH71HH | ch7 1hh | ch71hh | Flintshire | Sir Y Fflint | Mold WwTW | 1028 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323878 | 363683 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HJ | CH71HJ | ch7 1hj | ch71hj | Flintshire | Sir Y Fflint | Mold WwTW | 879 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323994 | 363588 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HL | CH71HL | ch7 1hl | ch71hl | Flintshire | Sir Y Fflint | Mold WwTW | 824 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324025 | 363531 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HN | CH71HN | ch7 1hn | ch71hn | Flintshire | Sir Y Fflint | Mold WwTW | 783 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324025 | 363435 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HP | CH71HP | ch7 1hp | ch71hp | Flintshire | Sir Y Fflint | Mold WwTW | 601 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324191 | 362919 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HQ | CH71HQ | ch7 1hq | ch71hq | Flintshire | Sir Y Fflint | Mold WwTW | 952 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323903 | 363575 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HR | CH71HR | ch7 1hr | ch71hr | Flintshire | Sir Y Fflint | Mold WwTW | 403 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324403 | 362936 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HS | CH71HS | ch7 1hs | ch71hs | Flintshire | Sir Y Fflint | Mold WwTW | 836 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323958 | 363408 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HT | CH71HT | ch7 1ht | ch71ht | Flintshire | Sir Y Fflint | Mold WwTW | 743 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324009 | 363188 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HU | CH71HU | ch7 1hu | ch71hu | Flintshire | Sir Y Fflint | Mold WwTW | 470 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324328 | 362933 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HW | CH71HW | ch7 1hw | ch71hw | Flintshire | Sir Y Fflint | Mold WwTW | 723 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324087 | 363428 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HX | CH71HX | ch7 1hx | ch71hx | Flintshire | Sir Y Fflint | Mold WwTW | 394 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324360 | 363084 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HY | CH71HY | ch7 1hy | ch71hy | Flintshire | Sir Y Fflint | Mold WwTW | 514 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324267 | 362964 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1HZ | CH71HZ | ch7 1hz | ch71hz | Flintshire | Sir Y Fflint | Mold WwTW | 843 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323933 | 363347 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JB | CH71JB | ch7 1jb | ch71jb | Flintshire | Sir Y Fflint | Mold WwTW | 927 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323877 | 363452 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JD | CH71JD | ch7 1jd | ch71jd | Flintshire | Sir Y Fflint | Mold WwTW | 913 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323888 | 363440 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JE | CH71JE | ch7 1je | ch71je | Flintshire | Sir Y Fflint | Mold WwTW | 692 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324060 | 363090 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JF | CH71JF | ch7 1jf | ch71jf | Flintshire | Sir Y Fflint | Mold WwTW | 757 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323997 | 363061 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JG | CH71JG | ch7 1jg | ch71jg | Flintshire | Sir Y Fflint | Mold WwTW | 756 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324007 | 363002 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JH | CH71JH | ch7 1jh | ch71jh | Flintshire | Sir Y Fflint | Mold WwTW | 832 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323929 | 363009 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JJ | CH71JJ | ch7 1jj | ch71jj | Flintshire | Sir Y Fflint | Mold WwTW | 823 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323958 | 362916 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JL | CH71JL | ch7 1jl | ch71jl | Flintshire | Sir Y Fflint | Mold WwTW | 490 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324261 | 363113 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JN | CH71JN | ch7 1jn | ch71jn | Flintshire | Sir Y Fflint | Mold WwTW | 586 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324164 | 363155 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JP | CH71JP | ch7 1jp | ch71jp | Flintshire | Sir Y Fflint | Mold WwTW | 643 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324112 | 363218 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JQ | CH71JQ | ch7 1jq | ch71jq | Flintshire | Sir Y Fflint | Mold WwTW | 886 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323885 | 362951 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JR | CH71JR | ch7 1jr | ch71jr | Flintshire | Sir Y Fflint | Mold WwTW | 394 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324375 | 363260 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JT | CH71JT | ch7 1jt | ch71jt | Flintshire | Sir Y Fflint | Mold WwTW | 466 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324286 | 363098 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JU | CH71JU | ch7 1ju | ch71ju | Flintshire | Sir Y Fflint | Mold WwTW | 562 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324188 | 363142 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JW | CH71JW | ch7 1jw | ch71jw | Flintshire | Sir Y Fflint | Mold WwTW | 445 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324315 | 363234 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JX | CH71JX | ch7 1jx | ch71jx | Flintshire | Sir Y Fflint | Mold WwTW | 504 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324265 | 363003 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JY | CH71JY | ch7 1jy | ch71jy | Flintshire | Sir Y Fflint | Mold WwTW | 668 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324101 | 363299 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1JZ | CH71JZ | ch7 1jz | ch71jz | Flintshire | Sir Y Fflint | Mold WwTW | 717 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324056 | 363319 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LA | CH71LA | ch7 1la | ch71la | Flintshire | Sir Y Fflint | Mold WwTW | 1331 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323786 | 364057 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LB | CH71LB | ch7 1lb | ch71lb | Flintshire | Sir Y Fflint | Mold WwTW | 1464 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324009 | 364402 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LD | CH71LD | ch7 1ld | ch71ld | Flintshire | Sir Y Fflint | Mold WwTW | 1503 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324052 | 364471 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LG | CH71LG | ch7 1lg | ch71lg | Flintshire | Sir Y Fflint | Mold WwTW | 1486 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324101 | 364476 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LH | CH71LH | ch7 1lh | ch71lh | Flintshire | Sir Y Fflint | Mold WwTW | 1263 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324163 | 364258 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LJ | CH71LJ | ch7 1lj | ch71lj | Flintshire | Sir Y Fflint | Mold WwTW | 1380 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324160 | 364387 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LL | CH71LL | ch7 1ll | ch71ll | Flintshire | Sir Y Fflint | Mold WwTW | 1301 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324199 | 364318 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LN | CH71LN | ch7 1ln | ch71ln | Flintshire | Sir Y Fflint | Mold WwTW | 1350 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324174 | 364361 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LP | CH71LP | ch7 1lp | ch71lp | Flintshire | Sir Y Fflint | Mold WwTW | 1462 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324068 | 364433 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LQ | CH71LQ | ch7 1lq | ch71lq | Flintshire | Sir Y Fflint | Mold WwTW | 1349 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324064 | 364301 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LR | CH71LR | ch7 1lr | ch71lr | Flintshire | Sir Y Fflint | Mold WwTW | 1473 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324088 | 364455 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LS | CH71LS | ch7 1ls | ch71ls | Flintshire | Sir Y Fflint | Mold WwTW | 1512 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323306 | 363588 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LT | CH71LT | ch7 1lt | ch71lt | Flintshire | Sir Y Fflint | Mold WwTW | 1537 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324343 | 364622 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LU | CH71LU | ch7 1lu | ch71lu | Flintshire | Sir Y Fflint | Mold WwTW | 1472 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324376 | 364563 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LW | CH71LW | ch7 1lw | ch71lw | Flintshire | Sir Y Fflint | Mold WwTW | 1388 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324119 | 364376 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LX | CH71LX | ch7 1lx | ch71lx | Flintshire | Sir Y Fflint | Mold WwTW | 1503 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323989 | 364436 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1LY | CH71LY | ch7 1ly | ch71ly | Flintshire | Sir Y Fflint | Mold WwTW | 1388 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 324540 | 364512 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NA | CH71NA | ch7 1na | ch71na | Flintshire | Sir Y Fflint | Mold WwTW | 1549 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324026 | 364509 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NB | CH71NB | ch7 1nb | ch71nb | Flintshire | Sir Y Fflint | Mold WwTW | 1564 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323946 | 364481 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1ND | CH71ND | ch7 1nd | ch71nd | Flintshire | Sir Y Fflint | Mold WwTW | 1536 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323774 | 364326 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NE | CH71NE | ch7 1ne | ch71ne | Flintshire | Sir Y Fflint | Mold WwTW | 1546 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323705 | 364278 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NF | CH71NF | ch7 1nf | ch71nf | Flintshire | Sir Y Fflint | Mold WwTW | 1587 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323682 | 364313 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NG | CH71NG | ch7 1ng | ch71ng | Flintshire | Sir Y Fflint | Mold WwTW | 1574 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323181 | 363264 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NJ | CH71NJ | ch7 1nj | ch71nj | Flintshire | Sir Y Fflint | Mold WwTW | 331 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 324526 | 362897 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NL | CH71NL | ch7 1nl | ch71nl | Flintshire | Sir Y Fflint | Mold WwTW | 1277 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323739 | 363919 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NN | CH71NN | ch7 1nn | ch71nn | Flintshire | Sir Y Fflint | Mold WwTW | 2229 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322563 | 363569 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NP | CH71NP | ch7 1np | ch71np | Flintshire | Sir Y Fflint | Mold WwTW | 1187 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323746 | 363772 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NQ | CH71NQ | ch7 1nq | ch71nq | Flintshire | Sir Y Fflint | Mold WwTW | 1684 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323642 | 364408 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NR | CH71NR | ch7 1nr | ch71nr | Flintshire | Sir Y Fflint | Mold WwTW | 1173 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323775 | 363791 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NS | CH71NS | ch7 1ns | ch71ns | Flintshire | Sir Y Fflint | Mold WwTW | 1345 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323425 | 363368 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NT | CH71NT | ch7 1nt | ch71nt | Flintshire | Sir Y Fflint | Mold WwTW | 1400 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323743 | 364112 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NU | CH71NU | ch7 1nu | ch71nu | Flintshire | Sir Y Fflint | Mold WwTW | 1322 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323548 | 363689 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NW | CH71NW | ch7 1nw | ch71nw | Flintshire | Sir Y Fflint | Mold WwTW | 1620 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323720 | 364390 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NX | CH71NX | ch7 1nx | ch71nx | Flintshire | Sir Y Fflint | Mold WwTW | 1475 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323293 | 363368 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NY | CH71NY | ch7 1ny | ch71ny | Flintshire | Sir Y Fflint | Mold WwTW | 1308 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323618 | 363794 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1NZ | CH71NZ | ch7 1nz | ch71nz | Flintshire | Sir Y Fflint | Mold WwTW | 1238 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323719 | 363825 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PA | CH71PA | ch7 1pa | ch71pa | Flintshire | Sir Y Fflint | Mold WwTW | 1095 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323796 | 363676 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PB | CH71PB | ch7 1pb | ch71pb | Flintshire | Sir Y Fflint | Mold WwTW | 1074 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323798 | 363636 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PD | CH71PD | ch7 1pd | ch71pd | Flintshire | Sir Y Fflint | Mold WwTW | 1137 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323723 | 363627 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PE | CH71PE | ch7 1pe | ch71pe | Flintshire | Sir Y Fflint | Mold WwTW | 1447 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323313 | 363305 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PF | CH71PF | ch7 1pf | ch71pf | Flintshire | Sir Y Fflint | Mold WwTW | 1086 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323765 | 363597 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PG | CH71PG | ch7 1pg | ch71pg | Flintshire | Sir Y Fflint | Mold WwTW | 1021 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323836 | 363594 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PH | CH71PH | ch7 1ph | ch71ph | Flintshire | Sir Y Fflint | Mold WwTW | 1057 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323781 | 363562 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PJ | CH71PJ | ch7 1pj | ch71pj | Flintshire | Sir Y Fflint | Mold WwTW | 1082 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323758 | 363572 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PL | CH71PL | ch7 1pl | ch71pl | Flintshire | Sir Y Fflint | Mold WwTW | 1060 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323756 | 363507 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PN | CH71PN | ch7 1pn | ch71pn | Flintshire | Sir Y Fflint | Mold WwTW | 1101 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323697 | 363459 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PP | CH71PP | ch7 1pp | ch71pp | Flintshire | Sir Y Fflint | Mold WwTW | 1188 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323594 | 363410 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PQ | CH71PQ | ch7 1pq | ch71pq | Flintshire | Sir Y Fflint | Mold WwTW | 1036 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323807 | 363569 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PR | CH71PR | ch7 1pr | ch71pr | Flintshire | Sir Y Fflint | Mold WwTW | 1161 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323618 | 363397 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PS | CH71PS | ch7 1ps | ch71ps | Flintshire | Sir Y Fflint | Mold WwTW | 1318 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323463 | 363424 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PT | CH71PT | ch7 1pt | ch71pt | Flintshire | Sir Y Fflint | Mold WwTW | 1395 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323402 | 363496 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PU | CH71PU | ch7 1pu | ch71pu | Flintshire | Sir Y Fflint | Mold WwTW | 1417 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323336 | 363219 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PW | CH71PW | ch7 1pw | ch71pw | Flintshire | Sir Y Fflint | Mold WwTW | 1095 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323680 | 363371 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PX | CH71PX | ch7 1px | ch71px | Flintshire | Sir Y Fflint | Mold WwTW | 1359 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323393 | 363196 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PY | CH71PY | ch7 1py | ch71py | Flintshire | Sir Y Fflint | Mold WwTW | 1324 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323431 | 363244 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1PZ | CH71PZ | ch7 1pz | ch71pz | Flintshire | Sir Y Fflint | Mold WwTW | 1632 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323177 | 363573 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QA | CH71QA | ch7 1qa | ch71qa | Flintshire | Sir Y Fflint | Mold WwTW | 1353 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323398 | 363101 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QB | CH71QB | ch7 1qb | ch71qb | Flintshire | Sir Y Fflint | Mold WwTW | 1463 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323289 | 363065 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QD | CH71QD | ch7 1qd | ch71qd | Flintshire | Sir Y Fflint | Mold WwTW | 1522 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323232 | 363038 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QE | CH71QE | ch7 1qe | ch71qe | Flintshire | Sir Y Fflint | Mold WwTW | 2210 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322611 | 363694 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QF | CH71QF | ch7 1qf | ch71qf | Flintshire | Sir Y Fflint | Mold WwTW | 1366 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323533 | 363760 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QG | CH71QG | ch7 1qg | ch71qg | Flintshire | Sir Y Fflint | Mold WwTW | 1328 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323532 | 363669 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QH | CH71QH | ch7 1qh | ch71qh | Flintshire | Sir Y Fflint | Mold WwTW | 1678 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323100 | 363444 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QJ | CH71QJ | ch7 1qj | ch71qj | Flintshire | Sir Y Fflint | Mold WwTW | 1270 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323560 | 363583 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QL | CH71QL | ch7 1ql | ch71ql | Flintshire | Sir Y Fflint | Mold WwTW | 1286 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323523 | 363525 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QN | CH71QN | ch7 1qn | ch71qn | Flintshire | Sir Y Fflint | Mold WwTW | 1839 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322966 | 363582 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QP | CH71QP | ch7 1qp | ch71qp | Flintshire | Sir Y Fflint | Mold WwTW | 1815 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322982 | 363547 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QQ | CH71QQ | ch7 1qq | ch71qq | Flintshire | Sir Y Fflint | Mold WwTW | 1393 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323422 | 363559 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QR | CH71QR | ch7 1qr | ch71qr | Flintshire | Sir Y Fflint | Mold WwTW | 2044 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322778 | 363677 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QS | CH71QS | ch7 1qs | ch71qs | Flintshire | Sir Y Fflint | Mold WwTW | 1765 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323046 | 363596 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QT | CH71QT | ch7 1qt | ch71qt | Flintshire | Sir Y Fflint | Mold WwTW | 1896 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 322877 | 363428 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QU | CH71QU | ch7 1qu | ch71qu | Flintshire | Sir Y Fflint | Mold WwTW | 1937 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322848 | 363504 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QW | CH71QW | ch7 1qw | ch71qw | Flintshire | Sir Y Fflint | Mold WwTW | 1850 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322939 | 363513 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QX | CH71QX | ch7 1qx | ch71qx | Flintshire | Sir Y Fflint | Mold WwTW | 2020 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322767 | 363522 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QY | CH71QY | ch7 1qy | ch71qy | Flintshire | Sir Y Fflint | Mold WwTW | 2036 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322748 | 363508 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1QZ | CH71QZ | ch7 1qz | ch71qz | Flintshire | Sir Y Fflint | Mold WwTW | 2209 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322597 | 363632 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RA | CH71RA | ch7 1ra | ch71ra | Flintshire | Sir Y Fflint | Mold WwTW | 1756 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323439 | 364308 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RB | CH71RB | ch7 1rb | ch71rb | Flintshire | Sir Y Fflint | Mold WwTW | 1732 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323454 | 364288 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RD | CH71RD | ch7 1rd | ch71rd | Flintshire | Sir Y Fflint | Mold WwTW | 1900 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323329 | 364400 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RE | CH71RE | ch7 1re | ch71re | Flintshire | Sir Y Fflint | Mold WwTW | 2120 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323092 | 364460 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RF | CH71RF | ch7 1rf | ch71rf | Flintshire | Sir Y Fflint | Mold WwTW | 1669 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 323809 | 364518 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RG | CH71RG | ch7 1rg | ch71rg | Flintshire | Sir Y Fflint | Mold WwTW | 2083 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323134 | 364454 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RH | CH71RH | ch7 1rh | ch71rh | Flintshire | Sir Y Fflint | Mold WwTW | 1700 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323445 | 364228 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RJ | CH71RJ | ch7 1rj | ch71rj | Flintshire | Sir Y Fflint | Mold WwTW | 966 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323877 | 363552 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RL | CH71RL | ch7 1rl | ch71rl | Flintshire | Sir Y Fflint | Mold WwTW | 2021 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323286 | 364532 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RN | CH71RN | ch7 1rn | ch71rn | Flintshire | Sir Y Fflint | Mold WwTW | 2111 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323132 | 364495 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RP | CH71RP | ch7 1rp | ch71rp | Flintshire | Sir Y Fflint | Mold WwTW | 2183 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323136 | 364609 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RQ | CH71RQ | ch7 1rq | ch71rq | Flintshire | Sir Y Fflint | Mold WwTW | 2136 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323105 | 364502 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RR | CH71RR | ch7 1rr | ch71rr | Flintshire | Sir Y Fflint | Mold WwTW | 2149 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323182 | 364608 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RS | CH71RS | ch7 1rs | ch71rs | Flintshire | Sir Y Fflint | Mold WwTW | 2144 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323119 | 364530 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RT | CH71RT | ch7 1rt | ch71rt | Flintshire | Sir Y Fflint | Mold WwTW | 2232 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323084 | 364625 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RU | CH71RU | ch7 1ru | ch71ru | Flintshire | Sir Y Fflint | Mold WwTW | 2157 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323239 | 364679 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RW | CH71RW | ch7 1rw | ch71rw | Flintshire | Sir Y Fflint | Mold WwTW | 1707 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323710 | 364493 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RX | CH71RX | ch7 1rx | ch71rx | Flintshire | Sir Y Fflint | Mold WwTW | 2028 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323176 | 364418 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RY | CH71RY | ch7 1ry | ch71ry | Flintshire | Sir Y Fflint | Mold WwTW | 1937 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323223 | 364331 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1RZ | CH71RZ | ch7 1rz | ch71rz | Flintshire | Sir Y Fflint | Mold WwTW | 1987 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323161 | 364332 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SA | CH71SA | ch7 1sa | ch71sa | Flintshire | Sir Y Fflint | Mold WwTW | 2088 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323034 | 364329 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SB | CH71SB | ch7 1sb | ch71sb | Flintshire | Sir Y Fflint | Mold WwTW | 2009 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323101 | 364287 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SD | CH71SD | ch7 1sd | ch71sd | Flintshire | Sir Y Fflint | Mold WwTW | 2021 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323068 | 364259 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SE | CH71SE | ch7 1se | ch71se | Flintshire | Sir Y Fflint | Mold WwTW | 1954 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323118 | 364214 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SF | CH71SF | ch7 1sf | ch71sf | Flintshire | Sir Y Fflint | Mold WwTW | 1938 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323098 | 364152 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SG | CH71SG | ch7 1sg | ch71sg | Flintshire | Sir Y Fflint | Mold WwTW | 1977 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323075 | 364189 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SH | CH71SH | ch7 1sh | ch71sh | Flintshire | Sir Y Fflint | Mold WwTW | 2306 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323091 | 364740 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SJ | CH71SJ | ch7 1sj | ch71sj | Flintshire | Sir Y Fflint | Mold WwTW | 2345 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323087 | 364792 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SL | CH71SL | ch7 1sl | ch71sl | Flintshire | Sir Y Fflint | Mold WwTW | 1850 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323349 | 364347 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SN | CH71SN | ch7 1sn | ch71sn | Flintshire | Sir Y Fflint | Mold WwTW | 551 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324467 | 363613 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SP | CH71SP | ch7 1sp | ch71sp | Flintshire | Sir Y Fflint | Mold WwTW | 1539 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323515 | 364058 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SQ | CH71SQ | ch7 1sq | ch71sq | Flintshire | Sir Y Fflint | Mold WwTW | 2065 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323291 | 364600 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SR | CH71SR | ch7 1sr | ch71sr | Flintshire | Sir Y Fflint | Mold WwTW | 1557 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323457 | 364006 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SS | CH71SS | ch7 1ss | ch71ss | Flintshire | Sir Y Fflint | Mold WwTW | 1632 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323412 | 364073 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SU | CH71SU | ch7 1su | ch71su | Flintshire | Sir Y Fflint | Mold WwTW | 1719 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323265 | 364004 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SW | CH71SW | ch7 1sw | ch71sw | Flintshire | Sir Y Fflint | Mold WwTW | 2027 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323360 | 364615 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SX | CH71SX | ch7 1sx | ch71sx | Flintshire | Sir Y Fflint | Mold WwTW | 1865 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323005 | 363797 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SY | CH71SY | ch7 1sy | ch71sy | Flintshire | Sir Y Fflint | Mold WwTW | 1616 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323442 | 364088 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1SZ | CH71SZ | ch7 1sz | ch71sz | Flintshire | Sir Y Fflint | Mold WwTW | 1734 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323246 | 364002 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TA | CH71TA | ch7 1ta | ch71ta | Flintshire | Sir Y Fflint | Mold WwTW | 1608 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323381 | 363983 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TB | CH71TB | ch7 1tb | ch71tb | Flintshire | Sir Y Fflint | Mold WwTW | 1731 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323299 | 364083 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TD | CH71TD | ch7 1td | ch71td | Flintshire | Sir Y Fflint | Mold WwTW | 1831 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323163 | 364052 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TE | CH71TE | ch7 1te | ch71te | Flintshire | Sir Y Fflint | Mold WwTW | 1859 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323174 | 364125 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TF | CH71TF | ch7 1tf | ch71tf | Flintshire | Sir Y Fflint | Mold WwTW | 1906 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323063 | 364026 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TG | CH71TG | ch7 1tg | ch71tg | Flintshire | Sir Y Fflint | Mold WwTW | 2043 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322942 | 364090 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TH | CH71TH | ch7 1th | ch71th | Flintshire | Sir Y Fflint | Mold WwTW | 1923 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322956 | 363830 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TJ | CH71TJ | ch7 1tj | ch71tj | Flintshire | Sir Y Fflint | Mold WwTW | 1959 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322943 | 363895 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TL | CH71TL | ch7 1tl | ch71tl | Flintshire | Sir Y Fflint | Mold WwTW | 1782 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323092 | 363791 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TN | CH71TN | ch7 1tn | ch71tn | Flintshire | Sir Y Fflint | Mold WwTW | 1659 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323187 | 363695 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TQ | CH71TQ | ch7 1tq | ch71tq | Flintshire | Sir Y Fflint | Mold WwTW | 1965 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323000 | 364032 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TR | CH71TR | ch7 1tr | ch71tr | Flintshire | Sir Y Fflint | Mold WwTW | 1707 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323164 | 363771 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TS | CH71TS | ch7 1ts | ch71ts | Flintshire | Sir Y Fflint | Mold WwTW | 1710 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323128 | 363681 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TT | CH71TT | ch7 1tt | ch71tt | Flintshire | Sir Y Fflint | Mold WwTW | 2087 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322759 | 363763 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TU | CH71TU | ch7 1tu | ch71tu | Flintshire | Sir Y Fflint | Mold WwTW | 1991 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322889 | 363846 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TW | CH71TW | ch7 1tw | ch71tw | Flintshire | Sir Y Fflint | Mold WwTW | 1839 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323006 | 363721 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TX | CH71TX | ch7 1tx | ch71tx | Flintshire | Sir Y Fflint | Mold WwTW | 2075 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322802 | 363853 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TY | CH71TY | ch7 1ty | ch71ty | Flintshire | Sir Y Fflint | Mold WwTW | 2128 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322737 | 363829 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1TZ | CH71TZ | ch7 1tz | ch71tz | Flintshire | Sir Y Fflint | Mold WwTW | 2178 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322677 | 363806 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UA | CH71UA | ch7 1ua | ch71ua | Flintshire | Sir Y Fflint | Mold WwTW | 1624 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323465 | 364132 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UB | CH71UB | ch7 1ub | ch71ub | Flintshire | Sir Y Fflint | Mold WwTW | 1064 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324039 | 363931 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UD | CH71UD | ch7 1ud | ch71ud | Flintshire | Sir Y Fflint | Mold WwTW | 1260 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324027 | 364172 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UE | CH71UE | ch7 1ue | ch71ue | Flintshire | Sir Y Fflint | Mold WwTW | 897 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324298 | 363915 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UF | CH71UF | ch7 1uf | ch71uf | Flintshire | Sir Y Fflint | Mold WwTW | 905 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324323 | 363938 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UG | CH71UG | ch7 1ug | ch71ug | Flintshire | Sir Y Fflint | Mold WwTW | 801 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 324540 | 363913 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UH | CH71UH | ch7 1uh | ch71uh | Flintshire | Sir Y Fflint | Mold WwTW | 654 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 324722 | 363793 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UJ | CH71UJ | ch7 1uj | ch71uj | Flintshire | Sir Y Fflint | Mold WwTW | 695 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 324561 | 363809 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UL | CH71UL | ch7 1ul | ch71ul | Flintshire | Sir Y Fflint | Mold WwTW | 1288 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323658 | 363822 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UN | CH71UN | ch7 1un | ch71un | Flintshire | Sir Y Fflint | Mold WwTW | 640 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 324638 | 363770 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UP | CH71UP | ch7 1up | ch71up | Flintshire | Sir Y Fflint | Mold WwTW | 1526 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323309 | 363641 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UQ | CH71UQ | ch7 1uq | ch71uq | Flintshire | Sir Y Fflint | Mold WwTW | 727 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 324566 | 363843 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UR | CH71UR | ch7 1ur | ch71ur | Flintshire | Sir Y Fflint | Mold WwTW | 596 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324256 | 363473 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1US | CH71US | ch7 1us | ch71us | Flintshire | Sir Y Fflint | Mold WwTW | 569 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324429 | 363609 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UT | CH71UT | ch7 1ut | ch71ut | Flintshire | Sir Y Fflint | Mold WwTW | 631 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324388 | 363656 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UU | CH71UU | ch7 1uu | ch71uu | Flintshire | Sir Y Fflint | Mold WwTW | 663 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 324505 | 363756 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UW | CH71UW | ch7 1uw | ch71uw | Flintshire | Sir Y Fflint | Mold WwTW | 581 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 324530 | 363678 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UX | CH71UX | ch7 1ux | ch71ux | Flintshire | Sir Y Fflint | Mold WwTW | 724 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324315 | 363719 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UY | CH71UY | ch7 1uy | ch71uy | Flintshire | Sir Y Fflint | Mold WwTW | 818 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324310 | 363829 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1UZ | CH71UZ | ch7 1uz | ch71uz | Flintshire | Sir Y Fflint | Mold WwTW | 1600 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323237 | 363659 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1WP | CH71WP | ch7 1wp | ch71wp | Flintshire | Sir Y Fflint | Mold WwTW | 1004 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323806 | 363481 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1WT | CH71WT | ch7 1wt | ch71wt | Flintshire | Sir Y Fflint | Mold WwTW | 1666 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323406 | 364124 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XA | CH71XA | ch7 1xa | ch71xa | Flintshire | Sir Y Fflint | Mold WwTW | 940 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 324164 | 363874 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XB | CH71XB | ch7 1xb | ch71xb | Flintshire | Sir Y Fflint | Mold WwTW | 260 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 324543 | 362982 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XF | CH71XF | ch7 1xf | ch71xf | Flintshire | Sir Y Fflint | Mold WwTW | 1948 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323491 | 364626 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XG | CH71XG | ch7 1xg | ch71xg | Flintshire | Sir Y Fflint | Mold WwTW | 1768 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323370 | 364244 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XH | CH71XH | ch7 1xh | ch71xh | Flintshire | Sir Y Fflint | Mold WwTW | 1135 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323628 | 363306 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XJ | CH71XJ | ch7 1xj | ch71xj | Flintshire | Sir Y Fflint | Mold WwTW | 1139 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323616 | 363238 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XL | CH71XL | ch7 1xl | ch71xl | Flintshire | Sir Y Fflint | Mold WwTW | 1220 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323533 | 363224 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XN | CH71XN | ch7 1xn | ch71xn | Flintshire | Sir Y Fflint | Mold WwTW | 1570 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323222 | 362781 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XP | CH71XP | ch7 1xp | ch71xp | Flintshire | Sir Y Fflint | Mold WwTW | 592 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324340 | 362713 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XQ | CH71XQ | ch7 1xq | ch71xq | Flintshire | Sir Y Fflint | Mold WwTW | 1662 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323298 | 363948 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XR | CH71XR | ch7 1xr | ch71xr | Flintshire | Sir Y Fflint | Mold WwTW | 2101 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323332 | 364689 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XW | CH71XW | ch7 1xw | ch71xw | Flintshire | Sir Y Fflint | Mold WwTW | 1444 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323366 | 362730 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XY | CH71XY | ch7 1xy | ch71xy | Flintshire | Sir Y Fflint | Mold WwTW | 509 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324439 | 362737 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1XZ | CH71XZ | ch7 1xz | ch71xz | Flintshire | Sir Y Fflint | Mold WwTW | 514 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324393 | 362770 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1YA | CH71YA | ch7 1ya | ch71ya | Flintshire | Sir Y Fflint | Mold WwTW | 2298 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324083 | 365338 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1YG | CH71YG | ch7 1yg | ch71yg | Flintshire | Sir Y Fflint | Mold WwTW | 1718 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323602 | 364418 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1YR | CH71YR | ch7 1yr | ch71yr | Flintshire | Sir Y Fflint | Mold WwTW | 1835 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 323439 | 364423 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1YS | CH71YS | ch7 1ys | ch71ys | Flintshire | Sir Y Fflint | Mold WwTW | 2217 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323037 | 364546 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1YU | CH71YU | ch7 1yu | ch71yu | Flintshire | Sir Y Fflint | Mold WwTW | 618 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324134 | 363096 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1YX | CH71YX | ch7 1yx | ch71yx | Flintshire | Sir Y Fflint | Mold WwTW | 1598 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 323153 | 363145 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 1ZS | CH71ZS | ch7 1zs | ch71zs | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AA | CH72AA | ch7 2aa | ch72aa | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1688 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328493 | 363796 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AB | CH72AB | ch7 2ab | ch72ab | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1457 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328520 | 363533 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AD | CH72AD | ch7 2ad | ch72ad | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1471 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328553 | 363533 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AE | CH72AE | ch7 2ae | ch72ae | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1246 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328431 | 363342 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AF | CH72AF | ch7 2af | ch72af | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1631 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328619 | 363678 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AG | CH72AG | ch7 2ag | ch72ag | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1126 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328130 | 363320 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AH | CH72AH | ch7 2ah | ch72ah | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1695 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328563 | 363775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AJ | CH72AJ | ch7 2aj | ch72aj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1051 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328146 | 363239 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AL | CH72AL | ch7 2al | ch72al | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1275 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328353 | 363407 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AN | CH72AN | ch7 2an | ch72an | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1370 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 328501 | 363446 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AP | CH72AP | ch7 2ap | ch72ap | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1379 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328356 | 363517 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AQ | CH72AQ | ch7 2aq | ch72aq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1629 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328362 | 363779 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AR | CH72AR | ch7 2ar | ch72ar | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1318 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328210 | 363498 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AS | CH72AS | ch7 2as | ch72as | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1337 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328282 | 363498 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AT | CH72AT | ch7 2at | ch72at | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1307 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328319 | 363454 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AU | CH72AU | ch7 2au | ch72au | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1435 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328276 | 363602 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AW | CH72AW | ch7 2aw | ch72aw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1408 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328432 | 363519 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AX | CH72AX | ch7 2ax | ch72ax | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1484 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328272 | 363653 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AY | CH72AY | ch7 2ay | ch72ay | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1410 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328255 | 363581 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2AZ | CH72AZ | ch7 2az | ch72az | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1275 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328175 | 363462 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BA | CH72BA | ch7 2ba | ch72ba | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1197 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328167 | 363384 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BB | CH72BB | ch7 2bb | ch72bb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1302 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328102 | 363504 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BD | CH72BD | ch7 2bd | ch72bd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1194 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328062 | 363401 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BE | CH72BE | ch7 2be | ch72be | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1158 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327641 | 363351 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BF | CH72BF | ch7 2bf | ch72bf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1742 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328704 | 363759 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BG | CH72BG | ch7 2bg | ch72bg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1343 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328086 | 363548 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BH | CH72BH | ch7 2bh | ch72bh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1201 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 327412 | 363321 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BJ | CH72BJ | ch7 2bj | ch72bj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1041 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327651 | 363233 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BL | CH72BL | ch7 2bl | ch72bl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1087 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327580 | 363261 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BN | CH72BN | ch7 2bn | ch72bn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 795 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327799 | 363010 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BP | CH72BP | ch7 2bp | ch72bp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1166 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327796 | 363382 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BQ | CH72BQ | ch7 2bq | ch72bq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1405 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328055 | 363615 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BR | CH72BR | ch7 2br | ch72br | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1129 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327792 | 363344 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BS | CH72BS | ch7 2bs | ch72bs | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1239 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 327487 | 363391 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BT | CH72BT | ch7 2bt | ch72bt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1052 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327806 | 363268 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BU | CH72BU | ch7 2bu | ch72bu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1069 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327790 | 363284 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BW | CH72BW | ch7 2bw | ch72bw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1174 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327868 | 363393 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BX | CH72BX | ch7 2bx | ch72bx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1046 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327686 | 363246 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BY | CH72BY | ch7 2by | ch72by | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1142 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 327417 | 363259 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2BZ | CH72BZ | ch7 2bz | ch72bz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1133 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 327486 | 363278 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DA | CH72DA | ch7 2da | ch72da | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1525 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328241 | 363704 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DB | CH72DB | ch7 2db | ch72db | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1288 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 327475 | 363439 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DD | CH72DD | ch7 2dd | ch72dd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1359 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 327342 | 363463 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DF | CH72DF | ch7 2df | ch72df | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1423 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327579 | 363608 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DG | CH72DG | ch7 2dg | ch72dg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1199 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327828 | 363417 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DH | CH72DH | ch7 2dh | ch72dh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1701 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328853 | 363621 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DJ | CH72DJ | ch7 2dj | ch72dj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1493 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328029 | 363706 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DL | CH72DL | ch7 2dl | ch72dl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1500 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328167 | 363694 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DN | CH72DN | ch7 2dn | ch72dn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1577 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328152 | 363775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DP | CH72DP | ch7 2dp | ch72dp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1677 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327889 | 363896 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DQ | CH72DQ | ch7 2dq | ch72dq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 968 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328017 | 363179 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DR | CH72DR | ch7 2dr | ch72dr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 912 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327927 | 363131 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DT | CH72DT | ch7 2dt | ch72dt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1033 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328071 | 363237 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2DY | CH72DY | ch7 2dy | ch72dy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1502 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327595 | 363692 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2ED | CH72ED | ch7 2ed | ch72ed | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1783 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327922 | 364002 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2EE | CH72EE | ch7 2ee | ch72ee | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1761 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328239 | 363945 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2EF | CH72EF | ch7 2ef | ch72ef | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1751 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327975 | 363968 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2EG | CH72EG | ch7 2eg | ch72eg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1751 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327977 | 363968 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2EH | CH72EH | ch7 2eh | ch72eh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1762 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328289 | 363936 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2EN | CH72EN | ch7 2en | ch72en | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1798 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328199 | 363991 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2EP | CH72EP | ch7 2ep | ch72ep | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1742 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328392 | 363888 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2EQ | CH72EQ | ch7 2eq | ch72eq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1313 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327958 | 363531 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2ER | CH72ER | ch7 2er | ch72er | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1770 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328571 | 363853 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2ES | CH72ES | ch7 2es | ch72es | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1798 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328562 | 363887 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2ET | CH72ET | ch7 2et | ch72et | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1799 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328574 | 363883 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2EU | CH72EU | ch7 2eu | ch72eu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1745 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328535 | 363841 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2EW | CH72EW | ch7 2ew | ch72ew | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1828 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328255 | 364011 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2EX | CH72EX | ch7 2ex | ch72ex | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1827 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328039 | 364040 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2EY | CH72EY | ch7 2ey | ch72ey | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1443 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327945 | 363661 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2GA | CH72GA | ch7 2ga | ch72ga | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2187 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327500 | 364371 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2GB | CH72GB | ch7 2gb | ch72gb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2061 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327661 | 364268 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2GD | CH72GD | ch7 2gd | ch72gd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2083 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327548 | 364274 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2GE | CH72GE | ch7 2ge | ch72ge | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2099 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327604 | 364299 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2GW | CH72GW | ch7 2gw | ch72gw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2399 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327440 | 364576 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2GX | CH72GX | ch7 2gx | ch72gx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2341 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327430 | 364515 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2GY | CH72GY | ch7 2gy | ch72gy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2290 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327481 | 364472 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2GZ | CH72GZ | ch7 2gz | ch72gz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2259 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327507 | 364446 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HA | CH72HA | ch7 2ha | ch72ha | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1876 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327977 | 364093 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HB | CH72HB | ch7 2hb | ch72hb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1827 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327942 | 364046 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HD | CH72HD | ch7 2hd | ch72hd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1856 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328079 | 364066 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HE | CH72HE | ch7 2he | ch72he | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1887 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328123 | 364092 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HF | CH72HF | ch7 2hf | ch72hf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1957 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328146 | 364160 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HG | CH72HG | ch7 2hg | ch72hg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1918 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328053 | 364130 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HH | CH72HH | ch7 2hh | ch72hh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1471 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327899 | 363690 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HJ | CH72HJ | ch7 2hj | ch72hj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1854 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328037 | 364068 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HL | CH72HL | ch7 2hl | ch72hl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1806 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328496 | 363921 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HN | CH72HN | ch7 2hn | ch72hn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1845 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328491 | 363964 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HP | CH72HP | ch7 2hp | ch72hp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1658 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328261 | 363835 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HQ | CH72HQ | ch7 2hq | ch72hq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1874 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328154 | 364075 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HR | CH72HR | ch7 2hr | ch72hr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1778 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328154 | 363978 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HS | CH72HS | ch7 2hs | ch72hs | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1685 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328233 | 363869 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HW | CH72HW | ch7 2hw | ch72hw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1748 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328631 | 363803 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HX | CH72HX | ch7 2hx | ch72hx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1590 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328233 | 363772 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HY | CH72HY | ch7 2hy | ch72hy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1743 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327759 | 363957 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2HZ | CH72HZ | ch7 2hz | ch72hz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1971 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327196 | 364064 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JA | CH72JA | ch7 2ja | ch72ja | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1806 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327664 | 364011 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JB | CH72JB | ch7 2jb | ch72jb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1824 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327727 | 364036 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JD | CH72JD | ch7 2jd | ch72jd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1987 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327562 | 364179 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JE | CH72JE | ch7 2je | ch72je | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1763 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327612 | 363960 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JF | CH72JF | ch7 2jf | ch72jf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2059 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327521 | 364245 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JG | CH72JG | ch7 2jg | ch72jg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1965 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327467 | 364138 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JH | CH72JH | ch7 2jh | ch72jh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2041 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326901 | 364005 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JL | CH72JL | ch7 2jl | ch72jl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1636 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327831 | 363854 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JN | CH72JN | ch7 2jn | ch72jn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1375 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327881 | 363595 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JP | CH72JP | ch7 2jp | ch72jp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1654 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327856 | 363873 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JQ | CH72JQ | ch7 2jq | ch72jq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1947 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327497 | 364126 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JR | CH72JR | ch7 2jr | ch72jr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2145 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327413 | 364311 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JS | CH72JS | ch7 2js | ch72js | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1244 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327868 | 363463 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JT | CH72JT | ch7 2jt | ch72jt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1741 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327722 | 363952 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JU | CH72JU | ch7 2ju | ch72ju | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1742 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327708 | 363952 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JW | CH72JW | ch7 2jw | ch72jw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1076 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327948 | 363294 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JX | CH72JX | ch7 2jx | ch72jx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1441 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327801 | 363658 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JY | CH72JY | ch7 2jy | ch72jy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1303 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327797 | 363519 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2JZ | CH72JZ | ch7 2jz | ch72jz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1336 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327777 | 363551 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LA | CH72LA | ch7 2la | ch72la | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1382 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327760 | 363595 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LB | CH72LB | ch7 2lb | ch72lb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1766 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327490 | 363940 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LD | CH72LD | ch7 2ld | ch72ld | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1728 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327478 | 363898 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LE | CH72LE | ch7 2le | ch72le | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1651 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327380 | 363790 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LF | CH72LF | ch7 2lf | ch72lf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1653 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327556 | 363838 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LG | CH72LG | ch7 2lg | ch72lg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1563 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327425 | 363712 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LH | CH72LH | ch7 2lh | ch72lh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1574 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327482 | 363740 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LJ | CH72LJ | ch7 2lj | ch72lj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1627 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327585 | 363818 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LL | CH72LL | ch7 2ll | ch72ll | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1546 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327573 | 363733 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LN | CH72LN | ch7 2ln | ch72ln | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1599 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327699 | 363807 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LP | CH72LP | ch7 2lp | ch72lp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1423 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327732 | 363634 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LQ | CH72LQ | ch7 2lq | ch72lq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1574 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327519 | 363749 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LR | CH72LR | ch7 2lr | ch72lr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1242 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327759 | 363455 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LS | CH72LS | ch7 2ls | ch72ls | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1219 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327703 | 363424 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LT | CH72LT | ch7 2lt | ch72lt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1296 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327553 | 363471 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LU | CH72LU | ch7 2lu | ch72lu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1226 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327587 | 363408 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LW | CH72LW | ch7 2lw | ch72lw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1556 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327643 | 363756 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LX | CH72LX | ch7 2lx | ch72lx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1322 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327568 | 363502 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LY | CH72LY | ch7 2ly | ch72ly | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1496 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327665 | 363698 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2LZ | CH72LZ | ch7 2lz | ch72lz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1356 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327539 | 363529 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NA | CH72NA | ch7 2na | ch72na | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1362 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327585 | 363547 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NB | CH72NB | ch7 2nb | ch72nb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2420 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327065 | 364494 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2ND | CH72ND | ch7 2nd | ch72nd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2339 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327224 | 364461 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NE | CH72NE | ch7 2ne | ch72ne | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2146 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327233 | 364262 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NF | CH72NF | ch7 2nf | ch72nf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2259 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327111 | 364340 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NG | CH72NG | ch7 2ng | ch72ng | Flintshire | Sir Y Fflint | Mold WwTW | 1913 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326503 | 363905 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NH | CH72NH | ch7 2nh | ch72nh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1884 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327250 | 363991 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NJ | CH72NJ | ch7 2nj | ch72nj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1897 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327364 | 364042 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NL | CH72NL | ch7 2nl | ch72nl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1894 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327424 | 364055 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NN | CH72NN | ch7 2nn | ch72nn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2202 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327168 | 364299 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NP | CH72NP | ch7 2np | ch72np | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2014 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327236 | 364124 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NQ | CH72NQ | ch7 2nq | ch72nq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1807 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327483 | 363980 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NR | CH72NR | ch7 2nr | ch72nr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2092 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327184 | 364189 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NS | CH72NS | ch7 2ns | ch72ns | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2025 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326985 | 364031 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NT | CH72NT | ch7 2nt | ch72nt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2032 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326915 | 364002 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NU | CH72NU | ch7 2nu | ch72nu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2027 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326839 | 363952 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NW | CH72NW | ch7 2nw | ch72nw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2156 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327183 | 364256 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NX | CH72NX | ch7 2nx | ch72nx | Flintshire | Sir Y Fflint | Mold WwTW | 2051 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326626 | 363968 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NY | CH72NY | ch7 2ny | ch72ny | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1433 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327530 | 363607 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2NZ | CH72NZ | ch7 2nz | ch72nz | Flintshire | Sir Y Fflint | Mold WwTW | 1967 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326533 | 363969 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PA | CH72PA | ch7 2pa | ch72pa | Flintshire | Sir Y Fflint | Mold WwTW | 1979 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326512 | 364040 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PB | CH72PB | ch7 2pb | ch72pb | Flintshire | Sir Y Fflint | Mold WwTW | 1907 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326533 | 363815 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PD | CH72PD | ch7 2pd | ch72pd | Flintshire | Sir Y Fflint | Mold WwTW | 1930 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326533 | 363878 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PE | CH72PE | ch7 2pe | ch72pe | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1902 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327070 | 363935 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PF | CH72PF | ch7 2pf | ch72pf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1890 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327030 | 363902 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PG | CH72PG | ch7 2pg | ch72pg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1320 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 327496 | 363479 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PH | CH72PH | ch7 2ph | ch72ph | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1910 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326975 | 363896 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PJ | CH72PJ | ch7 2pj | ch72pj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1943 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326991 | 363942 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PL | CH72PL | ch7 2pl | ch72pl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1993 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326767 | 363866 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PN | CH72PN | ch7 2pn | ch72pn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2030 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326763 | 363908 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PP | CH72PP | ch7 2pp | ch72pp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1851 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326904 | 363786 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PQ | CH72PQ | ch7 2pq | ch72pq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1729 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326950 | 363670 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PR | CH72PR | ch7 2pr | ch72pr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1912 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326814 | 363800 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PS | CH72PS | ch7 2ps | ch72ps | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1034 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 327211 | 363000 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PT | CH72PT | ch7 2pt | ch72pt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1746 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327089 | 363771 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PU | CH72PU | ch7 2pu | ch72pu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1582 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327305 | 363689 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PW | CH72PW | ch7 2pw | ch72pw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1811 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326939 | 363760 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PX | CH72PX | ch7 2px | ch72px | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1697 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327235 | 363785 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PY | CH72PY | ch7 2py | ch72py | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1514 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327397 | 363651 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2PZ | CH72PZ | ch7 2pz | ch72pz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1431 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327424 | 363572 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QA | CH72QA | ch7 2qa | ch72qa | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1701 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327029 | 363686 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QB | CH72QB | ch7 2qb | ch72qb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1611 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327160 | 363655 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QD | CH72QD | ch7 2qd | ch72qd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1564 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327155 | 363600 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QE | CH72QE | ch7 2qe | ch72qe | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1554 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327122 | 363570 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QF | CH72QF | ch7 2qf | ch72qf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1473 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327202 | 363522 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QG | CH72QG | ch7 2qg | ch72qg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1575 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327037 | 363543 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QH | CH72QH | ch7 2qh | ch72qh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1973 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326635 | 363742 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QJ | CH72QJ | ch7 2qj | ch72qj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1318 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328407 | 363432 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QL | CH72QL | ch7 2ql | ch72ql | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1346 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 328375 | 363475 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QN | CH72QN | ch7 2qn | ch72qn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1563 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328393 | 363699 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QP | CH72QP | ch7 2qp | ch72qp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1483 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328396 | 363613 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QQ | CH72QQ | ch7 2qq | ch72qq | Flintshire | Sir Y Fflint | Mold WwTW | 1897 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 326555 | 363721 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QR | CH72QR | ch7 2qr | ch72qr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2464 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327209 | 364587 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QS | CH72QS | ch7 2qs | ch72qs | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2428 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327128 | 364525 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QT | CH72QT | ch7 2qt | ch72qt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2434 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327164 | 364542 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QU | CH72QU | ch7 2qu | ch72qu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2540 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327135 | 364644 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QW | CH72QW | ch7 2qw | ch72qw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1873 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327145 | 363938 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QX | CH72QX | ch7 2qx | ch72qx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2599 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327133 | 364705 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QY | CH72QY | ch7 2qy | ch72qy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2420 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327345 | 364577 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2QZ | CH72QZ | ch7 2qz | ch72qz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1997 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327359 | 364144 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2RA | CH72RA | ch7 2ra | ch72ra | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1773 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327678 | 363980 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2RB | CH72RB | ch7 2rb | ch72rb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1391 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 327282 | 363471 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2RD | CH72RD | ch7 2rd | ch72rd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1472 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327284 | 363561 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2RE | CH72RE | ch7 2re | ch72re | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2348 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327355 | 364505 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2RF | CH72RF | ch7 2rf | ch72rf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1712 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327674 | 363918 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2SA | CH72SA | ch7 2sa | ch72sa | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1212 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327676 | 363413 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2TA | CH72TA | ch7 2ta | ch72ta | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2005 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 327040 | 364035 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 2TB | CH72TB | ch7 2tb | ch72tb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1846 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328587 | 363929 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AA | CH73AA | ch7 3aa | ch73aa | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2100 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 329173 | 363882 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AB | CH73AB | ch7 3ab | ch73ab | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1987 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328960 | 363893 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AD | CH73AD | ch7 3ad | ch73ad | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1876 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328668 | 363926 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AE | CH73AE | ch7 3ae | ch73ae | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1822 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328746 | 363828 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AF | CH73AF | ch7 3af | ch73af | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1885 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328800 | 363870 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AG | CH73AG | ch7 3ag | ch73ag | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2134 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 329497 | 363623 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AH | CH73AH | ch7 3ah | ch73ah | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1870 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 329026 | 363705 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AJ | CH73AJ | ch7 3aj | ch73aj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2267 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329623 | 363681 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AL | CH73AL | ch7 3al | ch73al | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1800 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328924 | 363693 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AN | CH73AN | ch7 3an | ch73an | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1788 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328958 | 363653 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AP | CH73AP | ch7 3ap | ch73ap | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1757 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 329124 | 363470 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AQ | CH73AQ | ch7 3aq | ch73aq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1841 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328878 | 363773 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AR | CH73AR | ch7 3ar | ch73ar | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2030 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 329070 | 363871 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AS | CH73AS | ch7 3as | ch73as | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1785 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328893 | 363696 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AT | CH73AT | ch7 3at | ch73at | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1729 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328920 | 363608 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AU | CH73AU | ch7 3au | ch73au | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2024 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 329245 | 363722 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AW | CH73AW | ch7 3aw | ch73aw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1813 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328968 | 363677 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AX | CH73AX | ch7 3ax | ch73ax | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2105 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 329246 | 363829 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AY | CH73AY | ch7 3ay | ch73ay | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1996 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 329537 | 363346 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3AZ | CH73AZ | ch7 3az | ch73az | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1985 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 329090 | 363801 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BA | CH73BA | ch7 3ba | ch73ba | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1807 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 329017 | 363632 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BB | CH73BB | ch7 3bb | ch73bb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2056 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 329618 | 363333 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BD | CH73BD | ch7 3bd | ch73bd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1881 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 329593 | 363018 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BE | CH73BE | ch7 3be | ch73be | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1626 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328823 | 363551 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BF | CH73BF | ch7 3bf | ch73bf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1876 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327782 | 364092 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BH | CH73BH | ch7 3bh | ch73bh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1610 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328848 | 363513 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BJ | CH73BJ | ch7 3bj | ch73bj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1536 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 328757 | 363487 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BL | CH73BL | ch7 3bl | ch73bl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1414 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 328691 | 363385 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BN | CH73BN | ch7 3bn | ch73bn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1141 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 328627 | 363091 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BP | CH73BP | ch7 3bp | ch73bp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1550 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328665 | 363562 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BQ | CH73BQ | ch7 3bq | ch73bq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1674 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328954 | 363511 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BR | CH73BR | ch7 3br | ch73br | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1404 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 328622 | 363417 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BS | CH73BS | ch7 3bs | ch73bs | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1453 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 328608 | 363483 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BT | CH73BT | ch7 3bt | ch73bt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1520 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328581 | 363573 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BU | CH73BU | ch7 3bu | ch73bu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1544 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328707 | 363529 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BW | CH73BW | ch7 3bw | ch73bw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1611 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328642 | 363644 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BX | CH73BX | ch7 3bx | ch73bx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2098 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 329606 | 363425 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BY | CH73BY | ch7 3by | ch73by | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2152 | 812 | 700to900 | 1.63 | 1.19 | 0.87 | 15.13 | 8.07 | 8.92 | 329656 | 363448 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3BZ | CH73BZ | ch7 3bz | ch73bz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2209 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329645 | 363560 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DA | CH73DA | ch7 3da | ch73da | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1998 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328731 | 364032 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DB | CH73DB | ch7 3db | ch73db | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1967 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328643 | 364036 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DD | CH73DD | ch7 3dd | ch73dd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2596 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327256 | 364737 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DE | CH73DE | ch7 3de | ch73de | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2620 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327311 | 364774 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DF | CH73DF | ch7 3df | ch73df | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2453 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327283 | 364596 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DG | CH73DG | ch7 3dg | ch73dg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2548 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327225 | 364679 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DH | CH73DH | ch7 3dh | ch73dh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3147 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329433 | 364962 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DJ | CH73DJ | ch7 3dj | ch73dj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2648 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327155 | 364763 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DL | CH73DL | ch7 3dl | ch73dl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2033 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328653 | 364104 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DN | CH73DN | ch7 3dn | ch73dn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2844 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329422 | 364615 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DP | CH73DP | ch7 3dp | ch73dp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1994 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328627 | 364072 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DQ | CH73DQ | ch7 3dq | ch73dq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2053 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328623 | 364137 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DS | CH73DS | ch7 3ds | ch73ds | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2568 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 329437 | 364269 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DT | CH73DT | ch7 3dt | ch73dt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2618 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 329364 | 364383 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DU | CH73DU | ch7 3du | ch73du | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2578 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 329180 | 364451 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DX | CH73DX | ch7 3dx | ch73dx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2736 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 329466 | 364455 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DY | CH73DY | ch7 3dy | ch73dy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2973 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 329779 | 364515 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3DZ | CH73DZ | ch7 3dz | ch73dz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2612 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329059 | 364555 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EA | CH73EA | ch7 3ea | ch73ea | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2786 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329461 | 364520 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EB | CH73EB | ch7 3eb | ch73eb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2692 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329586 | 364309 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3ED | CH73ED | ch7 3ed | ch73ed | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2793 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329610 | 364419 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EE | CH73EE | ch7 3ee | ch73ee | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2755 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329627 | 364357 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EF | CH73EF | ch7 3ef | ch73ef | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2716 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329638 | 364297 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EG | CH73EG | ch7 3eg | ch73eg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2818 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329677 | 364398 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EH | CH73EH | ch7 3eh | ch73eh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2914 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329391 | 364716 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EJ | CH73EJ | ch7 3ej | ch73ej | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2947 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329431 | 364731 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EL | CH73EL | ch7 3el | ch73el | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2784 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329277 | 364633 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EN | CH73EN | ch7 3en | ch73en | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3099 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329295 | 364981 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EP | CH73EP | ch7 3ep | ch73ep | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2856 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329220 | 364746 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EQ | CH73EQ | ch7 3eq | ch73eq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2971 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329499 | 364716 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3ER | CH73ER | ch7 3er | ch73er | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2810 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329315 | 364641 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3ES | CH73ES | ch7 3es | ch73es | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2893 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329332 | 364727 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3ET | CH73ET | ch7 3et | ch73et | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2709 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 328932 | 364720 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EU | CH73EU | ch7 3eu | ch73eu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2789 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329238 | 364660 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EW | CH73EW | ch7 3ew | ch73ew | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2953 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329216 | 364857 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EX | CH73EX | ch7 3ex | ch73ex | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2881 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329775 | 364397 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EY | CH73EY | ch7 3ey | ch73ey | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2907 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329750 | 364453 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3EZ | CH73EZ | ch7 3ez | ch73ez | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2939 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329779 | 364470 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3FA | CH73FA | ch7 3fa | ch73fa | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2865 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329818 | 364338 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3FB | CH73FB | ch7 3fb | ch73fb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2048 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328730 | 364087 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3FD | CH73FD | ch7 3fd | ch73fd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2061 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328797 | 364070 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3FE | CH73FE | ch7 3fe | ch73fe | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2022 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328695 | 364074 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3FF | CH73FF | ch7 3ff | ch73ff | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2607 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 328806 | 364660 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3FG | CH73FG | ch7 3fg | ch73fg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2595 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328220 | 364793 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3FH | CH73FH | ch7 3fh | ch73fh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2775 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 328753 | 364856 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3FJ | CH73FJ | ch7 3fj | ch73fj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2469 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328979 | 364435 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3FL | CH73FL | ch7 3fl | ch73fl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2505 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 328762 | 364567 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3FN | CH73FN | ch7 3fn | ch73fn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1888 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328907 | 363810 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3FP | CH73FP | ch7 3fp | ch73fp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2975 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 329376 | 364796 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3FQ | CH73FQ | ch7 3fq | ch73fq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2626 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327387 | 364796 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GA | CH73GA | ch7 3ga | ch73ga | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1911 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328669 | 363964 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GB | CH73GB | ch7 3gb | ch73gb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1909 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328781 | 363908 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GD | CH73GD | ch7 3gd | ch73gd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1997 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328828 | 363982 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GE | CH73GE | ch7 3ge | ch73ge | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1976 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328738 | 364004 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GF | CH73GF | ch7 3gf | ch73gf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1930 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328871 | 363881 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GG | CH73GG | ch7 3gg | ch73gg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2484 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327291 | 364630 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GH | CH73GH | ch7 3gh | ch73gh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2319 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328724 | 364383 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GJ | CH73GJ | ch7 3gj | ch73gj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2263 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328736 | 364318 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GL | CH73GL | ch7 3gl | ch73gl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2178 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328585 | 364283 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GN | CH73GN | ch7 3gn | ch73gn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2140 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328667 | 364213 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GP | CH73GP | ch7 3gp | ch73gp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2260 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328796 | 364290 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GQ | CH73GQ | ch7 3gq | ch73gq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2309 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328836 | 364326 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3GR | CH73GR | ch7 3gr | ch73gr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2398 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328837 | 364422 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HA | CH73HA | ch7 3ha | ch73ha | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1895 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327836 | 364114 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HB | CH73HB | ch7 3hb | ch73hb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1892 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327864 | 364111 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HD | CH73HD | ch7 3hd | ch73hd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1811 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327876 | 364030 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HE | CH73HE | ch7 3he | ch73he | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2139 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327896 | 364358 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HF | CH73HF | ch7 3hf | ch73hf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1988 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328252 | 364174 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HG | CH73HG | ch7 3hg | ch73hg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1963 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328216 | 364155 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HJ | CH73HJ | ch7 3hj | ch73hj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2074 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328004 | 364290 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HL | CH73HL | ch7 3hl | ch73hl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2062 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328071 | 364273 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HN | CH73HN | ch7 3hn | ch73hn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1882 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328310 | 364054 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HP | CH73HP | ch7 3hp | ch73hp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1973 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327966 | 364191 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HQ | CH73HQ | ch7 3hq | ch73hq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2201 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327694 | 364412 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HR | CH73HR | ch7 3hr | ch73hr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2062 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328138 | 364266 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HT | CH73HT | ch7 3ht | ch73ht | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1899 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328555 | 363998 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HU | CH73HU | ch7 3hu | ch73hu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1964 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327719 | 364176 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HW | CH73HW | ch7 3hw | ch73hw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1801 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328321 | 363968 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HX | CH73HX | ch7 3hx | ch73hx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2136 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327947 | 364355 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HY | CH73HY | ch7 3hy | ch73hy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1921 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327925 | 364140 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3HZ | CH73HZ | ch7 3hz | ch73hz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1939 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 327803 | 364156 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JA | CH73JA | ch7 3ja | ch73ja | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2147 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328395 | 364306 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JB | CH73JB | ch7 3jb | ch73jb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2240 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328427 | 364394 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JD | CH73JD | ch7 3jd | ch73jd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2269 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328584 | 364379 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JE | CH73JE | ch7 3je | ch73je | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1967 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328523 | 364082 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JF | CH73JF | ch7 3jf | ch73jf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2003 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328473 | 364136 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JG | CH73JG | ch7 3jg | ch73jg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2026 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328538 | 364139 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JH | CH73JH | ch7 3jh | ch73jh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2315 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328483 | 364457 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JJ | CH73JJ | ch7 3jj | ch73jj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2356 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328424 | 364514 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JL | CH73JL | ch7 3jl | ch73jl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2672 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328238 | 364868 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JN | CH73JN | ch7 3jn | ch73jn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2608 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328264 | 364800 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JP | CH73JP | ch7 3jp | ch73jp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2510 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328297 | 364696 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JQ | CH73JQ | ch7 3jq | ch73jq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2117 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328555 | 364229 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JR | CH73JR | ch7 3jr | ch73jr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2079 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328284 | 364261 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JS | CH73JS | ch7 3js | ch73js | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2651 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329779 | 364078 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JT | CH73JT | ch7 3jt | ch73jt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2680 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329751 | 364147 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JU | CH73JU | ch7 3ju | ch73ju | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2107 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328450 | 364251 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JW | CH73JW | ch7 3jw | ch73jw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2589 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329751 | 364018 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JY | CH73JY | ch7 3jy | ch73jy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2596 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 328588 | 364719 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3JZ | CH73JZ | ch7 3jz | ch73jz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2751 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 329746 | 364249 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LA | CH73LA | ch7 3la | ch73la | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2333 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328514 | 364467 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LB | CH73LB | ch7 3lb | ch73lb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2511 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 328523 | 364649 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LD | CH73LD | ch7 3ld | ch73ld | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2293 | 821 | 700to900 | 1.64 | 1.2 | 0.88 | 15.3 | 8.16 | 9.02 | 328569 | 364409 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LE | CH73LE | ch7 3le | ch73le | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2414 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 328536 | 364545 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LF | CH73LF | ch7 3lf | ch73lf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2375 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328490 | 364517 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LG | CH73LG | ch7 3lg | ch73lg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2544 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 328508 | 364687 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LH | CH73LH | ch7 3lh | ch73lh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2909 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328245 | 365106 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LJ | CH73LJ | ch7 3lj | ch73lj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2859 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328254 | 365055 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LL | CH73LL | ch7 3ll | ch73ll | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3209 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328448 | 365379 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LN | CH73LN | ch7 3ln | ch73ln | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3501 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 328459 | 365673 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LP | CH73LP | ch7 3lp | ch73lp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3320 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328404 | 365499 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LR | CH73LR | ch7 3lr | ch73lr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3362 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 328434 | 365537 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LS | CH73LS | ch7 3ls | ch73ls | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3569 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 328489 | 365737 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LT | CH73LT | ch7 3lt | ch73lt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3777 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 328553 | 365937 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LU | CH73LU | ch7 3lu | ch73lu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3794 | 797 | 700to900 | 1.6 | 1.17 | 0.86 | 14.85 | 7.92 | 8.76 | 328615 | 365943 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LW | CH73LW | ch7 3lw | ch73lw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3229 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 328569 | 365376 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LX | CH73LX | ch7 3lx | ch73lx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3433 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 328484 | 365600 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LY | CH73LY | ch7 3ly | ch73ly | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2942 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 328994 | 364946 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3LZ | CH73LZ | ch7 3lz | ch73lz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3346 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 328376 | 365529 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NA | CH73NA | ch7 3na | ch73na | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2247 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328364 | 364416 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NB | CH73NB | ch7 3nb | ch73nb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2523 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328099 | 364733 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3ND | CH73ND | ch7 3nd | ch73nd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2602 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328145 | 364809 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NE | CH73NE | ch7 3ne | ch73ne | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2457 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327987 | 364674 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NF | CH73NF | ch7 3nf | ch73nf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2541 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327980 | 364759 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NG | CH73NG | ch7 3ng | ch73ng | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2393 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328237 | 364587 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NH | CH73NH | ch7 3nh | ch73nh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2416 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328269 | 364605 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NJ | CH73NJ | ch7 3nj | ch73nj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2756 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327982 | 364974 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NL | CH73NL | ch7 3nl | ch73nl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2680 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328000 | 364897 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NN | CH73NN | ch7 3nn | ch73nn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2856 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327351 | 365024 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NP | CH73NP | ch7 3np | ch73np | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2992 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327670 | 365203 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NQ | CH73NQ | ch7 3nq | ch73nq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2440 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328179 | 364642 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NR | CH73NR | ch7 3nr | ch73nr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2983 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327479 | 365174 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NS | CH73NS | ch7 3ns | ch73ns | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3652 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 327450 | 365844 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NT | CH73NT | ch7 3nt | ch73nt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3381 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 327454 | 365572 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NU | CH73NU | ch7 3nu | ch73nu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2893 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327595 | 365097 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NW | CH73NW | ch7 3nw | ch73nw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2926 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327695 | 365139 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NX | CH73NX | ch7 3nx | ch73nx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2906 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327544 | 365104 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NY | CH73NY | ch7 3ny | ch73ny | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2891 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327462 | 365078 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3NZ | CH73NZ | ch7 3nz | ch73nz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2901 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327529 | 365097 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PA | CH73PA | ch7 3pa | ch73pa | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2797 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327477 | 364985 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PB | CH73PB | ch7 3pb | ch73pb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2710 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327600 | 364914 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PD | CH73PD | ch7 3pd | ch73pd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2572 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327424 | 364749 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PE | CH73PE | ch7 3pe | ch73pe | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2593 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327469 | 364778 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PF | CH73PF | ch7 3pf | ch73pf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2562 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327656 | 364770 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PG | CH73PG | ch7 3pg | ch73pg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2521 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327589 | 364722 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PH | CH73PH | ch7 3ph | ch73ph | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2831 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327556 | 365030 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PJ | CH73PJ | ch7 3pj | ch73pj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2345 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327752 | 364560 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PL | CH73PL | ch7 3pl | ch73pl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3058 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327649 | 365267 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PN | CH73PN | ch7 3pn | ch73pn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2451 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328130 | 364658 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PP | CH73PP | ch7 3pp | ch73pp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2842 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327943 | 365061 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PQ | CH73PQ | ch7 3pq | ch73pq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2389 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327759 | 364605 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PR | CH73PR | ch7 3pr | ch73pr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2763 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327575 | 364964 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PS | CH73PS | ch7 3ps | ch73ps | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3089 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327845 | 365308 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PT | CH73PT | ch7 3pt | ch73pt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2520 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327840 | 364739 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PU | CH73PU | ch7 3pu | ch73pu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2982 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327905 | 365201 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PW | CH73PW | ch7 3pw | ch73pw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2293 | 831 | 700to900 | 1.66 | 1.22 | 0.89 | 15.49 | 8.26 | 9.13 | 328283 | 364478 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PX | CH73PX | ch7 3px | ch73px | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2843 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327427 | 365024 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PY | CH73PY | ch7 3py | ch73py | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2518 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 327890 | 364737 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3PZ | CH73PZ | ch7 3pz | ch73pz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3394 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 328417 | 365572 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3QA | CH73QA | ch7 3qa | ch73qa | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2891 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328363 | 365071 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3QB | CH73QB | ch7 3qb | ch73qb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3004 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328449 | 365170 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3QD | CH73QD | ch7 3qd | ch73qd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3007 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328345 | 365191 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3QE | CH73QE | ch7 3qe | ch73qe | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2914 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328416 | 365085 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3QF | CH73QF | ch7 3qf | ch73qf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2824 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328342 | 365007 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3QG | CH73QG | ch7 3qg | ch73qg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2763 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328381 | 364938 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3QH | CH73QH | ch7 3qh | ch73qh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2739 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328255 | 364934 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3QJ | CH73QJ | ch7 3qj | ch73qj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2747 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328408 | 364917 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3QL | CH73QL | ch7 3ql | ch73ql | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2704 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328460 | 364862 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3QP | CH73QP | ch7 3qp | ch73qp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2640 | 817 | 700to900 | 1.64 | 1.2 | 0.88 | 15.23 | 8.12 | 8.98 | 328437 | 364802 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 3ZJ | CH73ZJ | ch7 3zj | ch73zj | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AB | CH74AB | ch7 4ab | ch74ab | Flintshire | Sir Y Fflint | Mold WwTW | 2800 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 321954 | 362999 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AD | CH74AD | ch7 4ad | ch74ad | Flintshire | Sir Y Fflint | Mold WwTW | 2727 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 322034 | 362905 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AE | CH74AE | ch7 4ae | ch74ae | Flintshire | Sir Y Fflint | Mold WwTW | 1857 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 322904 | 362947 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AF | CH74AF | ch7 4af | ch74af | Flintshire | Sir Y Fflint | Mold WwTW | 2780 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 322003 | 362718 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AG | CH74AG | ch7 4ag | ch74ag | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1991 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326864 | 360137 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AH | CH74AH | ch7 4ah | ch74ah | Flintshire | Sir Y Fflint | Mold WwTW | 2781 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 321983 | 362872 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AJ | CH74AJ | ch7 4aj | ch74aj | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1944 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327001 | 360044 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AL | CH74AL | ch7 4al | ch74al | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 632 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324912 | 358101 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AN | CH74AN | ch7 4an | ch74an | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2651 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 321807 | 363073 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AP | CH74AP | ch7 4ap | ch74ap | Flintshire | Sir Y Fflint | Mold WwTW | 2816 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 321954 | 362814 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AQ | CH74AQ | ch7 4aq | ch74aq | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1719 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326875 | 359850 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AR | CH74AR | ch7 4ar | ch74ar | Flintshire | Sir Y Fflint | Mold WwTW | 2828 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 321952 | 362735 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AS | CH74AS | ch7 4as | ch74as | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2785 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 321859 | 362697 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AT | CH74AT | ch7 4at | ch74at | Flintshire | Sir Y Fflint | Mold WwTW | 2677 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 322136 | 362568 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AU | CH74AU | ch7 4au | ch74au | Flintshire | Sir Y Fflint | Mold WwTW | 3712 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 321860 | 360813 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AY | CH74AY | ch7 4ay | ch74ay | Flintshire | Sir Y Fflint | Grainnrhyd STW | 3979 | 986 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.38 | 9.8 | 10.83 | 322001 | 360019 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4AZ | CH74AZ | ch7 4az | ch74az | Flintshire | Sir Y Fflint | Maes Y Groes STW | 3582 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 321441 | 360705 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4BA | CH74BA | ch7 4ba | ch74ba | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 2132 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 323692 | 359026 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4BD | CH74BD | ch7 4bd | ch74bd | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 1777 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 324472 | 359364 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4BE | CH74BE | ch7 4be | ch74be | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 1661 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 324153 | 358873 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4BF | CH74BF | ch7 4bf | ch74bf | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 2135 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 320305 | 357825 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4BG | CH74BG | ch7 4bg | ch74bg | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 1239 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 324286 | 358031 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4BH | CH74BH | ch7 4bh | ch74bh | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1678 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326839 | 359818 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4BJ | CH74BJ | ch7 4bj | ch74bj | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 1878 | 969 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.06 | 9.63 | 10.65 | 323644 | 357859 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4BL | CH74BL | ch7 4bl | ch74bl | Flintshire | Sir Y Fflint | Grainnrhyd STW | 2201 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 323053 | 357649 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4BN | CH74BN | ch7 4bn | ch74bn | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1567 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326963 | 359653 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4BP | CH74BP | ch7 4bp | ch74bp | Flintshire | Sir Y Fflint | Grainnrhyd STW | 2035 | 989 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.43 | 9.83 | 10.87 | 323483 | 356604 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4BQ | CH74BQ | ch7 4bq | ch74bq | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 1575 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 324053 | 357358 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4BR | CH74BR | ch7 4br | ch74br | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 1628 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 320914 | 357580 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4BS | CH74BS | ch7 4bs | ch74bs | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 1266 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 322733 | 356432 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4BT | CH74BT | ch7 4bt | ch74bt | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 2305 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 320225 | 357976 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4BU | CH74BU | ch7 4bu | ch74bu | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 1641 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 321240 | 357686 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4BW | CH74BW | ch7 4bw | ch74bw | Flintshire | Sir Y Fflint | Grainnrhyd STW | 1541 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 321972 | 357543 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4BX | CH74BX | ch7 4bx | ch74bx | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 2189 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 320379 | 357937 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4BY | CH74BY | ch7 4by | ch74by | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 2203 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 320319 | 357916 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4BZ | CH74BZ | ch7 4bz | ch74bz | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 2414 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 320011 | 358139 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4DA | CH74DA | ch7 4da | ch74da | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 2030 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 320260 | 357661 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4DB | CH74DB | ch7 4db | ch74db | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 2209 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 320734 | 358134 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4DD | CH74DD | ch7 4dd | ch74dd | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 3268 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 320797 | 359256 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4DH | CH74DH | ch7 4dh | ch74dh | Flintshire | Sir Y Fflint | Mold WwTW | 711 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324255 | 362630 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4DJ | CH74DJ | ch7 4dj | ch74dj | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 2279 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 319955 | 358017 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4DL | CH74DL | ch7 4dl | ch74dl | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 3563 | 962 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.93 | 9.56 | 10.57 | 322691 | 360094 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4DN | CH74DN | ch7 4dn | ch74dn | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 708 | 992 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.49 | 9.86 | 10.9 | 319727 | 355995 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4DP | CH74DP | ch7 4dp | ch74dp | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1780 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327280 | 359724 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4DR | CH74DR | ch7 4dr | ch74dr | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2795 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 321913 | 362864 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4DS | CH74DS | ch7 4ds | ch74ds | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2673 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 321796 | 362901 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4DT | CH74DT | ch7 4dt | ch74dt | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2716 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 321832 | 362863 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4DU | CH74DU | ch7 4du | ch74du | Flintshire | Sir Y Fflint | Mold WwTW | 3340 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 322028 | 361206 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4DW | CH74DW | ch7 4dw | ch74dw | Flintshire | Sir Y Fflint | Maes Y Groes STW | 3487 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 321052 | 360543 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4DX | CH74DX | ch7 4dx | ch74dx | Flintshire | Sir Y Fflint | Mold WwTW | 3224 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 321980 | 361492 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4DY | CH74DY | ch7 4dy | ch74dy | Flintshire | Sir Y Fflint | Maes Y Groes STW | 3059 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 321335 | 361310 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4DZ | CH74DZ | ch7 4dz | ch74dz | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 3263 | 962 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.93 | 9.56 | 10.57 | 322950 | 359938 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EA | CH74EA | ch7 4ea | ch74ea | Flintshire | Sir Y Fflint | Mold WwTW | 3349 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 322312 | 360845 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EB | CH74EB | ch7 4eb | ch74eb | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 2545 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 324067 | 360018 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4ED | CH74ED | ch7 4ed | ch74ed | Flintshire | Sir Y Fflint | Mold WwTW | 1345 | 893 | 700to900 | 1.79 | 1.31 | 0.96 | 16.64 | 8.88 | 9.81 | 323831 | 362158 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EE | CH74EE | ch7 4ee | ch74ee | Flintshire | Sir Y Fflint | Mold WwTW | 747 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324180 | 362657 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EF | CH74EF | ch7 4ef | ch74ef | Flintshire | Sir Y Fflint | Mold WwTW | 998 | 893 | 700to900 | 1.79 | 1.31 | 0.96 | 16.64 | 8.88 | 9.81 | 324222 | 362294 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EG | CH74EG | ch7 4eg | ch74eg | Flintshire | Sir Y Fflint | Mold WwTW | 2491 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 322732 | 361681 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EH | CH74EH | ch7 4eh | ch74eh | Flintshire | Sir Y Fflint | Mold WwTW | 2814 | 946 | 900to1200 | 1.89 | 1.39 | 1.02 | 17.63 | 9.4 | 10.39 | 322846 | 361069 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EJ | CH74EJ | ch7 4ej | ch74ej | Flintshire | Sir Y Fflint | Mold WwTW | 2597 | 946 | 900to1200 | 1.89 | 1.39 | 1.02 | 17.63 | 9.4 | 10.39 | 322949 | 361270 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EL | CH74EL | ch7 4el | ch74el | Flintshire | Sir Y Fflint | Mold WwTW | 2744 | 946 | 900to1200 | 1.89 | 1.39 | 1.02 | 17.63 | 9.4 | 10.39 | 323199 | 360877 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EN | CH74EN | ch7 4en | ch74en | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 2987 | 962 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.93 | 9.56 | 10.57 | 322820 | 359205 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EP | CH74EP | ch7 4ep | ch74ep | Flintshire | Sir Y Fflint | Mold WwTW | 2654 | 946 | 900to1200 | 1.89 | 1.39 | 1.02 | 17.63 | 9.4 | 10.39 | 323218 | 360974 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EQ | CH74EQ | ch7 4eq | ch74eq | Flintshire | Sir Y Fflint | Mold WwTW | 2451 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 322531 | 362101 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4ER | CH74ER | ch7 4er | ch74er | Flintshire | Sir Y Fflint | Mold WwTW | 2648 | 946 | 900to1200 | 1.89 | 1.39 | 1.02 | 17.63 | 9.4 | 10.39 | 323046 | 361114 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4ES | CH74ES | ch7 4es | ch74es | Flintshire | Sir Y Fflint | Mold WwTW | 2776 | 946 | 900to1200 | 1.89 | 1.39 | 1.02 | 17.63 | 9.4 | 10.39 | 323217 | 360827 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4ET | CH74ET | ch7 4et | ch74et | Flintshire | Sir Y Fflint | Mold WwTW | 2816 | 946 | 900to1200 | 1.89 | 1.39 | 1.02 | 17.63 | 9.4 | 10.39 | 323267 | 360747 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EU | CH74EU | ch7 4eu | ch74eu | Flintshire | Sir Y Fflint | Mold WwTW | 2823 | 946 | 900to1200 | 1.89 | 1.39 | 1.02 | 17.63 | 9.4 | 10.39 | 323302 | 360718 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EW | CH74EW | ch7 4ew | ch74ew | Flintshire | Sir Y Fflint | Mold WwTW | 2278 | 916 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.07 | 9.11 | 10.06 | 324066 | 360968 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EX | CH74EX | ch7 4ex | ch74ex | Flintshire | Sir Y Fflint | Mold WwTW | 2963 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 323561 | 360427 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EY | CH74EY | ch7 4ey | ch74ey | Flintshire | Sir Y Fflint | Mold WwTW | 2416 | 916 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.07 | 9.11 | 10.06 | 324027 | 360836 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4EZ | CH74EZ | ch7 4ez | ch74ez | Flintshire | Sir Y Fflint | Mold WwTW | 2860 | 946 | 900to1200 | 1.89 | 1.39 | 1.02 | 17.63 | 9.4 | 10.39 | 323323 | 360663 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4FA | CH74FA | ch7 4fa | ch74fa | Flintshire | Sir Y Fflint | Treuddyn WwTW | 1951 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 325164 | 359862 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4FB | CH74FB | ch7 4fb | ch74fb | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 2246 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 319856 | 358023 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4GA | CH74GA | ch7 4ga | ch74ga | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1726 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 327614 | 360517 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4GZ | CH74GZ | ch7 4gz | ch74gz | Flintshire | Sir Y Fflint | Mold WwTW | 1012 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 323753 | 362970 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HA | CH74HA | ch7 4ha | ch74ha | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1624 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 327616 | 360620 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HB | CH74HB | ch7 4hb | ch74hb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1232 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 329086 | 362512 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HD | CH74HD | ch7 4hd | ch74hd | Flintshire | Sir Y Fflint | Mold WwTW | 531 | 883 | 700to900 | 1.77 | 1.29 | 0.95 | 16.46 | 8.78 | 9.7 | 324257 | 362943 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HE | CH74HE | ch7 4he | ch74he | Flintshire | Sir Y Fflint | Mold WwTW | 505 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 324684 | 362639 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HF | CH74HF | ch7 4hf | ch74hf | Flintshire | Sir Y Fflint | Mold WwTW | 1890 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 325957 | 361687 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HG | CH74HG | ch7 4hg | ch74hg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1213 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 327277 | 361174 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HH | CH74HH | ch7 4hh | ch74hh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1502 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 327525 | 360764 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HJ | CH74HJ | ch7 4hj | ch74hj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1537 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 327541 | 360724 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HL | CH74HL | ch7 4hl | ch74hl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1697 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 327609 | 360547 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HN | CH74HN | ch7 4hn | ch74hn | Flintshire | Sir Y Fflint | Hope WwTW | 2534 | 842 | 700to900 | 1.69 | 1.23 | 0.9 | 15.69 | 8.37 | 9.25 | 328645 | 359746 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HP | CH74HP | ch7 4hp | ch74hp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2112 | 842 | 700to900 | 1.69 | 1.23 | 0.9 | 15.69 | 8.37 | 9.25 | 328637 | 360245 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HQ | CH74HQ | ch7 4hq | ch74hq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1249 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 327317 | 361111 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HR | CH74HR | ch7 4hr | ch74hr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1990 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 327780 | 360234 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HS | CH74HS | ch7 4hs | ch74hs | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1846 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 327683 | 360386 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HT | CH74HT | ch7 4ht | ch74ht | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2008 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 327711 | 360221 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HU | CH74HU | ch7 4hu | ch74hu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1701 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 327779 | 360523 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HW | CH74HW | ch7 4hw | ch74hw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1784 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 327734 | 360443 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HX | CH74HX | ch7 4hx | ch74hx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1649 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 327768 | 360576 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HY | CH74HY | ch7 4hy | ch74hy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1244 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 328415 | 361093 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4HZ | CH74HZ | ch7 4hz | ch74hz | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 799 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 328196 | 361482 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JA | CH74JA | ch7 4ja | ch74ja | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 673 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 327766 | 361559 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JB | CH74JB | ch7 4jb | ch74jb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 887 | 858 | 700to900 | 1.72 | 1.26 | 0.92 | 15.99 | 8.53 | 9.43 | 327584 | 361388 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JD | CH74JD | ch7 4jd | ch74jd | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 384 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 327509 | 362176 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JE | CH74JE | ch7 4je | ch74je | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 380 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 327510 | 362236 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JF | CH74JF | ch7 4jf | ch74jf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 755 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 328577 | 362533 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JG | CH74JG | ch7 4jg | ch74jg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1482 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 329284 | 362722 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JH | CH74JH | ch7 4jh | ch74jh | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 497 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 327489 | 362514 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JJ | CH74JJ | ch7 4jj | ch74jj | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1797 | 878 | 700to900 | 1.76 | 1.29 | 0.94 | 16.36 | 8.73 | 9.65 | 327659 | 360439 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JL | CH74JL | ch7 4jl | ch74jl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1265 | 846 | 700to900 | 1.69 | 1.24 | 0.91 | 15.77 | 8.41 | 9.29 | 326762 | 362792 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JN | CH74JN | ch7 4jn | ch74jn | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 129 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325392 | 357947 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JP | CH74JP | ch7 4jp | ch74jp | Flintshire | Sir Y Fflint | Mold WwTW | 1600 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 326186 | 362436 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JQ | CH74JQ | ch7 4jq | ch74jq | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1446 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 329265 | 362666 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JR | CH74JR | ch7 4jr | ch74jr | Flintshire | Sir Y Fflint | Mold WwTW | 1589 | 866 | 700to900 | 1.73 | 1.27 | 0.93 | 16.14 | 8.61 | 9.51 | 326114 | 362326 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JS | CH74JS | ch7 4js | ch74js | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 441 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327630 | 362576 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JT | CH74JT | ch7 4jt | ch74jt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 430 | 830 | 700to900 | 1.66 | 1.22 | 0.89 | 15.47 | 8.25 | 9.12 | 327603 | 362540 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JW | CH74JW | ch7 4jw | ch74jw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1487 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 326430 | 362501 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4JX | CH74JX | ch7 4jx | ch74jx | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 589 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324938 | 358020 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LA | CH74LA | ch7 4la | ch74la | Flintshire | Sir Y Fflint | Mold WwTW | 1613 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324849 | 361531 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LB | CH74LB | ch7 4lb | ch74lb | Flintshire | Sir Y Fflint | Mold WwTW | 1902 | 890 | 700to900 | 1.78 | 1.3 | 0.96 | 16.59 | 8.85 | 9.78 | 325256 | 361307 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LD | CH74LD | ch7 4ld | ch74ld | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 31 | 951 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.73 | 9.45 | 10.45 | 326345 | 358247 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LE | CH74LE | ch7 4le | ch74le | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 583 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325041 | 357598 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LF | CH74LF | ch7 4lf | ch74lf | Flintshire | Sir Y Fflint | Grainnrhyd STW | 2225 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 323744 | 356126 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LG | CH74LG | ch7 4lg | ch74lg | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 81 | 951 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.73 | 9.45 | 10.45 | 326269 | 358167 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LH | CH74LH | ch7 4lh | ch74lh | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 48 | 951 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.73 | 9.45 | 10.45 | 325564 | 357950 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LJ | CH74LJ | ch7 4lj | ch74lj | Flintshire | Sir Y Fflint | Treuddyn WwTW | 110 | 951 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.73 | 9.45 | 10.45 | 325777 | 357998 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LL | CH74LL | ch7 4ll | ch74ll | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 55 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325498 | 357880 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LN | CH74LN | ch7 4ln | ch74ln | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 317 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325263 | 358116 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LP | CH74LP | ch7 4lp | ch74lp | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 350 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325225 | 358118 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LQ | CH74LQ | ch7 4lq | ch74lq | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 303 | 951 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.73 | 9.45 | 10.45 | 326390 | 357923 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LR | CH74LR | ch7 4lr | ch74lr | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 38 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325487 | 357949 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LS | CH74LS | ch7 4ls | ch74ls | Flintshire | Sir Y Fflint | Treuddyn WwTW | 247 | 951 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.73 | 9.45 | 10.45 | 325581 | 358209 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LT | CH74LT | ch7 4lt | ch74lt | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 402 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325164 | 358116 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LU | CH74LU | ch7 4lu | ch74lu | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 485 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325038 | 357986 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LW | CH74LW | ch7 4lw | ch74lw | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 630 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324890 | 357919 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LX | CH74LX | ch7 4lx | ch74lx | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 421 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325101 | 357965 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LY | CH74LY | ch7 4ly | ch74ly | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 509 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325024 | 358044 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4LZ | CH74LZ | ch7 4lz | ch74lz | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 556 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325056 | 358236 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NA | CH74NA | ch7 4na | ch74na | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 640 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324995 | 358295 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NB | CH74NB | ch7 4nb | ch74nb | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 644 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325057 | 358378 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4ND | CH74ND | ch7 4nd | ch74nd | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 690 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 325145 | 358509 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NE | CH74NE | ch7 4ne | ch74ne | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 751 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 325135 | 358575 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NF | CH74NF | ch7 4nf | ch74nf | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 694 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324827 | 357964 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NG | CH74NG | ch7 4ng | ch74ng | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 766 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 325157 | 358604 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NH | CH74NH | ch7 4nh | ch74nh | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 774 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 325080 | 358566 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NJ | CH74NJ | ch7 4nj | ch74nj | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 742 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324787 | 358043 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NL | CH74NL | ch7 4nl | ch74nl | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 799 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324833 | 358338 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NN | CH74NN | ch7 4nn | ch74nn | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 943 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324584 | 357816 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NP | CH74NP | ch7 4np | ch74np | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 499 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325121 | 357630 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NQ | CH74NQ | ch7 4nq | ch74nq | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 755 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 325143 | 358584 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NS | CH74NS | ch7 4ns | ch74ns | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 2399 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 324356 | 355833 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NT | CH74NT | ch7 4nt | ch74nt | Flintshire | Sir Y Fflint | Grainnrhyd STW | 2267 | 986 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.38 | 9.8 | 10.83 | 323522 | 355007 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NU | CH74NU | ch7 4nu | ch74nu | Flintshire | Sir Y Fflint | Grainnrhyd STW | 2286 | 986 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.38 | 9.8 | 10.83 | 323514 | 354954 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NW | CH74NW | ch7 4nw | ch74nw | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 802 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324741 | 357739 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NX | CH74NX | ch7 4nx | ch74nx | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 368 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325182 | 358074 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NY | CH74NY | ch7 4ny | ch74ny | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 775 | 932 | 900to1200 | 1.87 | 1.36 | 1 | 17.37 | 9.26 | 10.24 | 325170 | 358621 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4NZ | CH74NZ | ch7 4nz | ch74nz | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 840 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324883 | 358477 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4PA | CH74PA | ch7 4pa | ch74pa | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 632 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324986 | 358267 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4PB | CH74PB | ch7 4pb | ch74pb | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 606 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324981 | 358207 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4PD | CH74PD | ch7 4pd | ch74pd | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 753 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 324788 | 357755 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4PE | CH74PE | ch7 4pe | ch74pe | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 110 | 967 | 900to1200 | 1.94 | 1.42 | 1.04 | 18.02 | 9.61 | 10.62 | 325443 | 358009 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4PX | CH74PX | ch7 4px | ch74px | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 328 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 319085 | 356260 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4PY | CH74PY | ch7 4py | ch74py | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 307 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 318865 | 356202 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4PZ | CH74PZ | ch7 4pz | ch74pz | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 157 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 318932 | 356066 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QA | CH74QA | ch7 4qa | ch74qa | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 723 | 995 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.55 | 9.89 | 10.93 | 320819 | 356247 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QD | CH74QD | ch7 4qd | ch74qd | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 1599 | 984 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.34 | 9.78 | 10.81 | 318257 | 357342 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QE | CH74QE | ch7 4qe | ch74qe | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 362 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 318952 | 356293 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QF | CH74QF | ch7 4qf | ch74qf | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 269 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 318844 | 356140 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QG | CH74QG | ch7 4qg | ch74qg | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 296 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 318895 | 356205 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QH | CH74QH | ch7 4qh | ch74qh | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 2033 | 933 | 900to1200 | 1.87 | 1.37 | 1 | 17.39 | 9.27 | 10.25 | 316993 | 355824 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QJ | CH74QJ | ch7 4qj | ch74qj | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 642 | 973 | 900to1200 | 1.95 | 1.42 | 1.04 | 18.14 | 9.67 | 10.69 | 318400 | 355779 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QL | CH74QL | ch7 4ql | ch74ql | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 637 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 318571 | 355488 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QN | CH74QN | ch7 4qn | ch74qn | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 414 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 319275 | 356265 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QP | CH74QP | ch7 4qp | ch74qp | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 214 | 995 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.55 | 9.89 | 10.93 | 321471 | 356278 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QQ | CH74QQ | ch7 4qq | ch74qq | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 485 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 318554 | 356066 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QR | CH74QR | ch7 4qr | ch74qr | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 198 | 995 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.55 | 9.89 | 10.93 | 321682 | 356183 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QS | CH74QS | ch7 4qs | ch74qs | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 930 | 995 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.55 | 9.89 | 10.93 | 322419 | 355832 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QT | CH74QT | ch7 4qt | ch74qt | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 1481 | 1009 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.81 | 10.03 | 11.09 | 322885 | 355497 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QU | CH74QU | ch7 4qu | ch74qu | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 885 | 1007 | 900to1200 | 2.02 | 1.47 | 1.08 | 18.77 | 10.01 | 11.06 | 321044 | 355324 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QW | CH74QW | ch7 4qw | ch74qw | Denbighshire | Sir Ddinbych | Grainnrhyd STW | 750 | 995 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.55 | 9.89 | 10.93 | 320770 | 356057 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QX | CH74QX | ch7 4qx | ch74qx | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 736 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 318891 | 355214 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4QY | CH74QY | ch7 4qy | ch74qy | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 170 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 319072 | 356100 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4RA | CH74RA | ch7 4ra | ch74ra | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1559 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 327239 | 359486 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RB | CH74RB | ch7 4rb | ch74rb | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1678 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327262 | 359615 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RD | CH74RD | ch7 4rd | ch74rd | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1777 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327322 | 359694 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RE | CH74RE | ch7 4re | ch74re | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1917 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327377 | 359825 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RF | CH74RF | ch7 4rf | ch74rf | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1896 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327407 | 359780 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RG | CH74RG | ch7 4rg | ch74rg | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1895 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327432 | 359761 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RH | CH74RH | ch7 4rh | ch74rh | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1770 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327211 | 359755 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RJ | CH74RJ | ch7 4rj | ch74rj | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1771 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327156 | 359786 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RL | CH74RL | ch7 4rl | ch74rl | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1714 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327150 | 359725 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RN | CH74RN | ch7 4rn | ch74rn | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1643 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326967 | 359734 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RP | CH74RP | ch7 4rp | ch74rp | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1641 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327045 | 359696 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RQ | CH74RQ | ch7 4rq | ch74rq | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1713 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327236 | 359673 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RR | CH74RR | ch7 4rr | ch74rr | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1616 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327027 | 359677 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RS | CH74RS | ch7 4rs | ch74rs | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1743 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326910 | 359863 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RT | CH74RT | ch7 4rt | ch74rt | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1664 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326959 | 359760 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RU | CH74RU | ch7 4ru | ch74ru | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1805 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327067 | 359867 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RW | CH74RW | ch7 4rw | ch74rw | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1744 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327044 | 359810 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RX | CH74RX | ch7 4rx | ch74rx | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1775 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327370 | 359658 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RY | CH74RY | ch7 4ry | ch74ry | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1554 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327174 | 359524 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4RZ | CH74RZ | ch7 4rz | ch74rz | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 2067 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327092 | 360141 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SB | CH74SB | ch7 4sb | ch74sb | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1961 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327075 | 360033 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SD | CH74SD | ch7 4sd | ch74sd | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1957 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327124 | 360008 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SE | CH74SE | ch7 4se | ch74se | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1927 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327134 | 359971 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SF | CH74SF | ch7 4sf | ch74sf | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 2011 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326925 | 360140 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SG | CH74SG | ch7 4sg | ch74sg | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1946 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326828 | 360101 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SH | CH74SH | ch7 4sh | ch74sh | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1986 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326653 | 360179 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SJ | CH74SJ | ch7 4sj | ch74sj | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1972 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326793 | 360136 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SL | CH74SL | ch7 4sl | ch74sl | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2055 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 326705 | 360542 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SN | CH74SN | ch7 4sn | ch74sn | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1963 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 326866 | 360546 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SP | CH74SP | ch7 4sp | ch74sp | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1917 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 326812 | 360636 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SQ | CH74SQ | ch7 4sq | ch74sq | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 2045 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326772 | 360216 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SR | CH74SR | ch7 4sr | ch74sr | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2042 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326822 | 360480 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SS | CH74SS | ch7 4ss | ch74ss | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2339 | 889 | 700to900 | 1.78 | 1.3 | 0.95 | 16.57 | 8.84 | 9.77 | 326002 | 360840 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4ST | CH74ST | ch7 4st | ch74st | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2051 | 889 | 700to900 | 1.78 | 1.3 | 0.95 | 16.57 | 8.84 | 9.77 | 326384 | 360829 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SU | CH74SU | ch7 4su | ch74su | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 2033 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327145 | 360082 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SW | CH74SW | ch7 4sw | ch74sw | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1950 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 326799 | 360604 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SX | CH74SX | ch7 4sx | ch74sx | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2097 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326734 | 360471 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SY | CH74SY | ch7 4sy | ch74sy | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2134 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326780 | 360398 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4SZ | CH74SZ | ch7 4sz | ch74sz | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1844 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327190 | 359850 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TA | CH74TA | ch7 4ta | ch74ta | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1868 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 327414 | 359740 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TB | CH74TB | ch7 4tb | ch74tb | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 1158 | 994 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.53 | 9.88 | 10.92 | 319806 | 356790 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4TD | CH74TD | ch7 4td | ch74td | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 1762 | 1003 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.69 | 9.97 | 11.02 | 319666 | 357577 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 4TE | CH74TE | ch7 4te | ch74te | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1284 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 327141 | 359215 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TF | CH74TF | ch7 4tf | ch74tf | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1384 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 327120 | 359356 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TG | CH74TG | ch7 4tg | ch74tg | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1135 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 327022 | 359119 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TH | CH74TH | ch7 4th | ch74th | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1356 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 327146 | 359302 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TJ | CH74TJ | ch7 4tj | ch74tj | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1139 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 327047 | 359105 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TL | CH74TL | ch7 4tl | ch74tl | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1135 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 327040 | 359105 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TN | CH74TN | ch7 4tn | ch74tn | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 835 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 326809 | 358903 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TP | CH74TP | ch7 4tp | ch74tp | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 744 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 326753 | 358832 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TQ | CH74TQ | ch7 4tq | ch74tq | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1426 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 327189 | 359358 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TR | CH74TR | ch7 4tr | ch74tr | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1422 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 327132 | 359394 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TS | CH74TS | ch7 4ts | ch74ts | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1220 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 326991 | 359245 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TT | CH74TT | ch7 4tt | ch74tt | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1275 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 327031 | 359285 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TU | CH74TU | ch7 4tu | ch74tu | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1509 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 327724 | 358796 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TW | CH74TW | ch7 4tw | ch74tw | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 808 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 326785 | 358887 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TX | CH74TX | ch7 4tx | ch74tx | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 875 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 326912 | 358873 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TY | CH74TY | ch7 4ty | ch74ty | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1812 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 328044 | 358807 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4TZ | CH74TZ | ch7 4tz | ch74tz | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 1153 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 327109 | 359069 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4UA | CH74UA | ch7 4ua | ch74ua | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 822 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 326863 | 358845 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4UB | CH74UB | ch7 4ub | ch74ub | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 767 | 919 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.13 | 9.14 | 10.1 | 326820 | 358810 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4UD | CH74UD | ch7 4ud | ch74ud | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2122 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326920 | 360333 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4UE | CH74UE | ch7 4ue | ch74ue | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 2143 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326864 | 360295 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4UF | CH74UF | ch7 4uf | ch74uf | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2080 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326884 | 360400 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4UG | CH74UG | ch7 4ug | ch74ug | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2034 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326871 | 360461 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4UH | CH74UH | ch7 4uh | ch74uh | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 2096 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326845 | 360251 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4UJ | CH74UJ | ch7 4uj | ch74uj | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 2124 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326992 | 360237 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4UL | CH74UL | ch7 4ul | ch74ul | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 1975 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326973 | 360471 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 4UQ | CH74UQ | ch7 4uq | ch74uq | Flintshire | Sir Y Fflint | Treuddyn Lodge Villas STW | 2062 | 900 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.77 | 8.95 | 9.89 | 326925 | 360194 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DA | CH75DA | ch7 5da | ch75da | Flintshire | Sir Y Fflint | Rhydymwyn STW | 2543 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 322664 | 364670 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DB | CH75DB | ch7 5db | ch75db | Flintshire | Sir Y Fflint | Rhydymwyn STW | 1828 | 894 | 700to900 | 1.79 | 1.31 | 0.96 | 16.66 | 8.89 | 9.82 | 321606 | 364814 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DD | CH75DD | ch7 5dd | ch75dd | Flintshire | Sir Y Fflint | Rhydymwyn STW | 1786 | 894 | 700to900 | 1.79 | 1.31 | 0.96 | 16.66 | 8.89 | 9.82 | 321677 | 364893 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DE | CH75DE | ch7 5de | ch75de | Flintshire | Sir Y Fflint | Rhydymwyn STW | 1534 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 321354 | 365035 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DF | CH75DF | ch7 5df | ch75df | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1730 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 320563 | 364542 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DG | CH75DG | ch7 5dg | ch75dg | Flintshire | Sir Y Fflint | Rhydymwyn STW | 1401 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 321294 | 365156 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DH | CH75DH | ch7 5dh | ch75dh | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1712 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 320584 | 364483 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DJ | CH75DJ | ch7 5dj | ch75dj | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1538 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 320342 | 364509 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DL | CH75DL | ch7 5dl | ch75dl | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1531 | 950 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.71 | 9.44 | 10.44 | 320376 | 364457 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DN | CH75DN | ch7 5dn | ch75dn | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1879 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 320786 | 364481 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DP | CH75DP | ch7 5dp | ch75dp | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1658 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 320485 | 364524 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DQ | CH75DQ | ch7 5dq | ch75dq | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1864 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 320765 | 364486 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DR | CH75DR | ch7 5dr | ch75dr | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1606 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 320517 | 364394 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DS | CH75DS | ch7 5ds | ch75ds | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1683 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 320591 | 364422 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DT | CH75DT | ch7 5dt | ch75dt | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1798 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 320639 | 364553 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DU | CH75DU | ch7 5du | ch75du | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1739 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 320604 | 364501 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DW | CH75DW | ch7 5dw | ch75dw | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1895 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 320777 | 364525 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DX | CH75DX | ch7 5dx | ch75dx | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1700 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 320633 | 364766 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DY | CH75DY | ch7 5dy | ch75dy | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1588 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 320500 | 364751 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5DZ | CH75DZ | ch7 5dz | ch75dz | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1454 | 950 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.71 | 9.44 | 10.44 | 320348 | 364368 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EA | CH75EA | ch7 5ea | ch75ea | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1451 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 320214 | 364517 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EB | CH75EB | ch7 5eb | ch75eb | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1207 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 319959 | 364652 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5ED | CH75ED | ch7 5ed | ch75ed | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1576 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 320720 | 363867 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EE | CH75EE | ch7 5ee | ch75ee | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1752 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 320726 | 364332 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EF | CH75EF | ch7 5ef | ch75ef | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 627 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 319600 | 365122 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EG | CH75EG | ch7 5eg | ch75eg | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 719 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 319636 | 365021 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EH | CH75EH | ch7 5eh | ch75eh | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 935 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 319518 | 364664 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EJ | CH75EJ | ch7 5ej | ch75ej | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1268 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 320015 | 364623 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EL | CH75EL | ch7 5el | ch75el | Flintshire | Sir Y Fflint | Maes Y Groes STW | 956 | 963 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.95 | 9.57 | 10.58 | 319334 | 364435 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EN | CH75EN | ch7 5en | ch75en | Flintshire | Sir Y Fflint | Maes Y Groes STW | 828 | 963 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.95 | 9.57 | 10.58 | 319312 | 364309 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EP | CH75EP | ch7 5ep | ch75ep | Flintshire | Sir Y Fflint | Maes Y Groes STW | 338 | 963 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.95 | 9.57 | 10.58 | 319119 | 363820 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EQ | CH75EQ | ch7 5eq | ch75eq | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 910 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 319697 | 364813 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5ER | CH75ER | ch7 5er | ch75er | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1212 | 950 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.71 | 9.44 | 10.44 | 320256 | 364065 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5ES | CH75ES | ch7 5es | ch75es | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1814 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 320938 | 363972 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5ET | CH75ET | ch7 5et | ch75et | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1667 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 320852 | 363605 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EU | CH75EU | ch7 5eu | ch75eu | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1109 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 319815 | 364653 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EW | CH75EW | ch7 5ew | ch75ew | Flintshire | Sir Y Fflint | Maes Y Groes STW | 341 | 963 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.95 | 9.57 | 10.58 | 319490 | 363651 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EX | CH75EX | ch7 5ex | ch75ex | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 718 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 319324 | 364818 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EY | CH75EY | ch7 5ey | ch75ey | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1591 | 950 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.71 | 9.44 | 10.44 | 320469 | 364436 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5EZ | CH75EZ | ch7 5ez | ch75ez | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 975 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 319209 | 364531 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5FA | CH75FA | ch7 5fa | ch75fa | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1463 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 320483 | 362806 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5FF | CH75FF | ch7 5ff | ch75ff | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1438 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 317782 | 366073 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5GA | CH75GA | ch7 5ga | ch75ga | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1787 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 320684 | 364673 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5GB | CH75GB | ch7 5gb | ch75gb | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1717 | 908 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.92 | 9.03 | 9.98 | 320573 | 364506 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HA | CH75HA | ch7 5ha | ch75ha | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1172 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 319386 | 366636 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HD | CH75HD | ch7 5hd | ch75hd | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 770 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 319644 | 366044 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HE | CH75HE | ch7 5he | ch75he | Flintshire | Sir Y Fflint | Rhydymwyn STW | 605 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 321445 | 366237 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HF | CH75HF | ch7 5hf | ch75hf | Flintshire | Sir Y Fflint | Rhydymwyn STW | 275 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 321158 | 366404 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HG | CH75HG | ch7 5hg | ch75hg | Flintshire | Sir Y Fflint | Rhydymwyn STW | 401 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 320609 | 366775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HH | CH75HH | ch7 5hh | ch75hh | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1171 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 319673 | 366521 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HL | CH75HL | ch7 5hl | ch75hl | Flintshire | Sir Y Fflint | Rhydymwyn STW | 892 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 320301 | 367161 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HN | CH75HN | ch7 5hn | ch75hn | Flintshire | Sir Y Fflint | Rhydymwyn STW | 520 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 320586 | 366914 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HP | CH75HP | ch7 5hp | ch75hp | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1655 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 318909 | 367143 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HQ | CH75HQ | ch7 5hq | ch75hq | Flintshire | Sir Y Fflint | Rhydymwyn STW | 541 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 320467 | 366824 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HR | CH75HR | ch7 5hr | ch75hr | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 905 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 318692 | 366307 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HS | CH75HS | ch7 5hs | ch75hs | Flintshire | Sir Y Fflint | Rhydymwyn STW | 564 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 320356 | 366350 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HT | CH75HT | ch7 5ht | ch75ht | Flintshire | Sir Y Fflint | Rhydymwyn STW | 885 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 320398 | 365771 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HU | CH75HU | ch7 5hu | ch75hu | Flintshire | Sir Y Fflint | Rhydymwyn STW | 1053 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 319883 | 366227 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HW | CH75HW | ch7 5hw | ch75hw | Flintshire | Sir Y Fflint | Rhydymwyn STW | 943 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 320335 | 367254 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HX | CH75HX | ch7 5hx | ch75hx | Flintshire | Sir Y Fflint | Rhydymwyn STW | 556 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 320485 | 366870 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HY | CH75HY | ch7 5hy | ch75hy | Flintshire | Sir Y Fflint | Maes Y Groes STW | 721 | 950 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.71 | 9.44 | 10.44 | 319616 | 364072 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5HZ | CH75HZ | ch7 5hz | ch75hz | Flintshire | Sir Y Fflint | Rhydymwyn STW | 734 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 320242 | 366824 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JA | CH75JA | ch7 5ja | ch75ja | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 531 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 319517 | 365171 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JB | CH75JB | ch7 5jb | ch75jb | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 852 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 319680 | 364876 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JD | CH75JD | ch7 5jd | ch75jd | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 945 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 319675 | 364751 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JE | CH75JE | ch7 5je | ch75je | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 973 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 319783 | 364807 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JF | CH75JF | ch7 5jf | ch75jf | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 889 | 930 | 900to1200 | 1.86 | 1.36 | 1 | 17.33 | 9.24 | 10.22 | 319964 | 365293 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JG | CH75JG | ch7 5jg | ch75jg | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1112 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 320211 | 365540 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JH | CH75JH | ch7 5jh | ch75jh | Flintshire | Sir Y Fflint | Rhydymwyn STW | 102 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 320840 | 366583 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JJ | CH75JJ | ch7 5jj | ch75jj | Flintshire | Sir Y Fflint | Rhydymwyn STW | 792 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 320419 | 367129 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JP | CH75JP | ch7 5jp | ch75jp | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2684 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 321858 | 363773 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JR | CH75JR | ch7 5jr | ch75jr | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2651 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 321822 | 363799 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JS | CH75JS | ch7 5js | ch75js | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2382 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 321567 | 363350 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JT | CH75JT | ch7 5jt | ch75jt | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2639 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 321610 | 362439 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JW | CH75JW | ch7 5jw | ch75jw | Flintshire | Sir Y Fflint | Maes Y Groes STW | 3129 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 321423 | 361300 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JX | CH75JX | ch7 5jx | ch75jx | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2658 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 320371 | 361110 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5JY | CH75JY | ch7 5jy | ch75jy | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2295 | 947 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.65 | 9.41 | 10.4 | 321276 | 362536 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5JZ | CH75JZ | ch7 5jz | ch75jz | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2171 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 321111 | 362479 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5LA | CH75LA | ch7 5la | ch75la | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2739 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 321739 | 362490 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5LB | CH75LB | ch7 5lb | ch75lb | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 1533 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 319931 | 362149 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5LD | CH75LD | ch7 5ld | ch75ld | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2128 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 320779 | 362075 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5LE | CH75LE | ch7 5le | ch75le | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2076 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 320900 | 362314 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5LF | CH75LF | ch7 5lf | ch75lf | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 1806 | 947 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.65 | 9.41 | 10.4 | 320738 | 362561 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5LG | CH75LG | ch7 5lg | ch75lg | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2451 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 321419 | 362472 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5LH | CH75LH | ch7 5lh | ch75lh | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 1085 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 319818 | 362606 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5LJ | CH75LJ | ch7 5lj | ch75lj | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 1511 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 320461 | 362673 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5LL | CH75LL | ch7 5ll | ch75ll | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1485 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 320494 | 362780 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5LN | CH75LN | ch7 5ln | ch75ln | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2861 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 321915 | 362623 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5LP | CH75LP | ch7 5lp | ch75lp | Flintshire | Sir Y Fflint | Maes Y Groes STW | 3429 | 978 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.23 | 9.72 | 10.75 | 321786 | 361251 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5LQ | CH75LQ | ch7 5lq | ch75lq | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1974 | 947 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.65 | 9.41 | 10.4 | 320956 | 362609 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5LR | CH75LR | ch7 5lr | ch75lr | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2767 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 320312 | 360962 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5LS | CH75LS | ch7 5ls | ch75ls | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2864 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 320214 | 360816 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5LT | CH75LT | ch7 5lt | ch75lt | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2691 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 320249 | 361017 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5LU | CH75LU | ch7 5lu | ch75lu | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2558 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 319887 | 361030 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5LW | CH75LW | ch7 5lw | ch75lw | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2837 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 321619 | 362026 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5LX | CH75LX | ch7 5lx | ch75lx | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2480 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 319905 | 361116 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5LY | CH75LY | ch7 5ly | ch75ly | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2589 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 319913 | 361005 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5LZ | CH75LZ | ch7 5lz | ch75lz | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2376 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 319808 | 361197 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5NA | CH75NA | ch7 5na | ch75na | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2714 | 964 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.97 | 9.58 | 10.59 | 321685 | 362425 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NB | CH75NB | ch7 5nb | ch75nb | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2301 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 321208 | 362386 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5ND | CH75ND | ch7 5nd | ch75nd | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2667 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 321727 | 362670 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NE | CH75NE | ch7 5ne | ch75ne | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 2062 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 317052 | 365738 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NF | CH75NF | ch7 5nf | ch75nf | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1278 | 988 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.41 | 9.82 | 10.86 | 317835 | 365320 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NG | CH75NG | ch7 5ng | ch75ng | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2231 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 321125 | 362380 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NH | CH75NH | ch7 5nh | ch75nh | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1445 | 988 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.41 | 9.82 | 10.86 | 317659 | 365401 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NJ | CH75NJ | ch7 5nj | ch75nj | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 533 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 319075 | 364968 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NL | CH75NL | ch7 5nl | ch75nl | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 928 | 988 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.41 | 9.82 | 10.86 | 318205 | 365256 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NN | CH75NN | ch7 5nn | ch75nn | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1452 | 988 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.41 | 9.82 | 10.86 | 317681 | 365194 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NP | CH75NP | ch7 5np | ch75np | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 2225 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 317599 | 367141 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NQ | CH75NQ | ch7 5nq | ch75nq | Flintshire | Sir Y Fflint | Maes Y Groes STW | 2399 | 961 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.91 | 9.55 | 10.56 | 321301 | 362352 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NR | CH75NR | ch7 5nr | ch75nr | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1363 | 988 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.41 | 9.82 | 10.86 | 317743 | 365372 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NS | CH75NS | ch7 5ns | ch75ns | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1289 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 317813 | 365569 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NT | CH75NT | ch7 5nt | ch75nt | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 992 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 318364 | 366165 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NU | CH75NU | ch7 5nu | ch75nu | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 2576 | 955 | 900to1200 | 1.91 | 1.4 | 1.03 | 17.8 | 9.49 | 10.49 | 317174 | 367209 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NW | CH75NW | ch7 5nw | ch75nw | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1666 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 317672 | 366357 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NX | CH75NX | ch7 5nx | ch75nx | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1990 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 317197 | 366081 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NY | CH75NY | ch7 5ny | ch75ny | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1794 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 317340 | 365846 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5NZ | CH75NZ | ch7 5nz | ch75nz | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 2678 | 977 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.21 | 9.71 | 10.73 | 316423 | 365482 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PA | CH75PA | ch7 5pa | ch75pa | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1971 | 975 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.17 | 9.69 | 10.71 | 317137 | 365325 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PB | CH75PB | ch7 5pb | ch75pb | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1838 | 975 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.17 | 9.69 | 10.71 | 317283 | 365226 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PD | CH75PD | ch7 5pd | ch75pd | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1668 | 988 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.41 | 9.82 | 10.86 | 317515 | 364982 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PE | CH75PE | ch7 5pe | ch75pe | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1611 | 988 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.41 | 9.82 | 10.86 | 317666 | 364768 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PF | CH75PF | ch7 5pf | ch75pf | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 2085 | 975 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.17 | 9.69 | 10.71 | 317200 | 364643 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PG | CH75PG | ch7 5pg | ch75pg | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1118 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 318337 | 364212 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PH | CH75PH | ch7 5ph | ch75ph | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1257 | 1010 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.82 | 10.04 | 11.1 | 318004 | 363074 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PJ | CH75PJ | ch7 5pj | ch75pj | Flintshire | Sir Y Fflint | Maes Y Groes STW | 1689 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 317524 | 363764 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PL | CH75PL | ch7 5pl | ch75pl | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1340 | 991 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.47 | 9.85 | 10.89 | 317760 | 365509 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PN | CH75PN | ch7 5pn | ch75pn | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1281 | 988 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.41 | 9.82 | 10.86 | 317856 | 365196 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PP | CH75PP | ch7 5pp | ch75pp | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1309 | 988 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.41 | 9.82 | 10.86 | 317812 | 365266 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PQ | CH75PQ | ch7 5pq | ch75pq | Flintshire | Sir Y Fflint | Maes Y Groes STW | 869 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 318479 | 363990 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5PR | CH75PR | ch7 5pr | ch75pr | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 1202 | 988 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.41 | 9.82 | 10.86 | 317932 | 365217 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5QA | CH75QA | ch7 5qa | ch75qa | Flintshire | Sir Y Fflint | Rhosesmor STW | 572 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 320989 | 367578 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5QB | CH75QB | ch7 5qb | ch75qb | Flintshire | Sir Y Fflint | Rhosesmor STW | 685 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 320611 | 367587 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5QD | CH75QD | ch7 5qd | ch75qd | Flintshire | Sir Y Fflint | Rhosesmor STW | 777 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 320331 | 367755 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5QE | CH75QE | ch7 5qe | ch75qe | Flintshire | Sir Y Fflint | Rhosesmor STW | 1666 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 319422 | 367616 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5QF | CH75QF | ch7 5qf | ch75qf | Flintshire | Sir Y Fflint | Rhosesmor STW | 1526 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 319548 | 367681 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5QG | CH75QG | ch7 5qg | ch75qg | Flintshire | Sir Y Fflint | Rhosesmor STW | 1707 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 319374 | 367633 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5QH | CH75QH | ch7 5qh | ch75qh | Flintshire | Sir Y Fflint | Rhosesmor STW | 1587 | 901 | 900to1200 | 1.8 | 1.32 | 0.97 | 16.79 | 8.96 | 9.9 | 319504 | 367623 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5QL | CH75QL | ch7 5ql | ch75ql | Flintshire | Sir Y Fflint | Cilcain Pantymwyn STW | 2198 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 318774 | 367673 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5QQ | CH75QQ | ch7 5qq | ch75qq | Flintshire | Sir Y Fflint | Rhosesmor STW | 1600 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 319476 | 367666 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5QW | CH75QW | ch7 5qw | ch75qw | Flintshire | Sir Y Fflint | Rhosesmor STW | 2416 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 318593 | 368350 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5QZ | CH75QZ | ch7 5qz | ch75qz | Flintshire | Sir Y Fflint | Rhydymwyn STW | 909 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 320200 | 367079 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 5SA | CH75SA | ch7 5sa | ch75sa | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 1172 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 319627 | 362403 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SB | CH75SB | ch7 5sb | ch75sb | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 1238 | 954 | 900to1200 | 1.91 | 1.4 | 1.02 | 17.78 | 9.48 | 10.48 | 319625 | 362331 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SE | CH75SE | ch7 5se | ch75se | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 922 | 988 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.41 | 9.82 | 10.86 | 319406 | 362594 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SF | CH75SF | ch7 5sf | ch75sf | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 1332 | 975 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.17 | 9.69 | 10.71 | 318941 | 362182 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SG | CH75SG | ch7 5sg | ch75sg | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 1494 | 975 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.17 | 9.69 | 10.71 | 319018 | 362006 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SH | CH75SH | ch7 5sh | ch75sh | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2627 | 996 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.56 | 9.9 | 10.94 | 318004 | 361147 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SJ | CH75SJ | ch7 5sj | ch75sj | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2194 | 996 | 900to1200 | 1.99 | 1.46 | 1.07 | 18.56 | 9.9 | 10.94 | 318450 | 361425 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SL | CH75SL | ch7 5sl | ch75sl | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2799 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 318753 | 360726 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SN | CH75SN | ch7 5sn | ch75sn | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 3235 | 998 | 900to1200 | 2 | 1.46 | 1.07 | 18.6 | 9.92 | 10.96 | 318785 | 360281 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SP | CH75SP | ch7 5sp | ch75sp | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2829 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 318801 | 360689 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SQ | CH75SQ | ch7 5sq | ch75sq | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 1694 | 975 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.17 | 9.69 | 10.71 | 318900 | 361822 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SR | CH75SR | ch7 5sr | ch75sr | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 3062 | 998 | 900to1200 | 2 | 1.46 | 1.07 | 18.6 | 9.92 | 10.96 | 318645 | 360478 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SS | CH75SS | ch7 5ss | ch75ss | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 3822 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 318202 | 359670 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5ST | CH75ST | ch7 5st | ch75st | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 3874 | 999 | 900to1200 | 2 | 1.46 | 1.07 | 18.62 | 9.93 | 10.98 | 318235 | 359737 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SX | CH75SX | ch7 5sx | ch75sx | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 2891 | 1001 | 900to1200 | 2 | 1.47 | 1.08 | 18.66 | 9.95 | 11 | 318825 | 360623 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5SY | CH75SY | ch7 5sy | ch75sy | Denbighshire | Sir Ddinbych | Maes Y Groes STW | 3131 | 998 | 900to1200 | 2 | 1.46 | 1.07 | 18.6 | 9.92 | 10.96 | 318759 | 360390 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5TA | CH75TA | ch7 5ta | ch75ta | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 2192 | 963 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.95 | 9.57 | 10.58 | 318564 | 358081 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5TF | CH75TF | ch7 5tf | ch75tf | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 2017 | 963 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.95 | 9.57 | 10.58 | 319156 | 357950 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5TG | CH75TG | ch7 5tg | ch75tg | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 3155 | 981 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.28 | 9.75 | 10.78 | 319226 | 359085 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5TQ | CH75TQ | ch7 5tq | ch75tq | Denbighshire | Sir Ddinbych | Llanarmon-Yn-Ial STW | 2066 | 963 | 900to1200 | 1.93 | 1.41 | 1.03 | 17.95 | 9.57 | 10.58 | 318918 | 358001 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
CH7 5XZ | CH75XZ | ch7 5xz | ch75xz | Flintshire | Sir Y Fflint | Rhydymwyn STW | 672 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 320366 | 366907 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AB | CH76AB | ch7 6ab | ch76ab | Flintshire | Sir Y Fflint | Rhosesmor STW | 3905 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 324821 | 367353 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AD | CH76AD | ch7 6ad | ch76ad | Flintshire | Sir Y Fflint | Mold WwTW | 3750 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 325053 | 366876 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AE | CH76AE | ch7 6ae | ch76ae | Flintshire | Sir Y Fflint | Rhydymwyn STW | 3529 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 324412 | 366839 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AH | CH76AH | ch7 6ah | ch76ah | Flintshire | Sir Y Fflint | Rhydymwyn STW | 3472 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 324318 | 367104 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AJ | CH76AJ | ch7 6aj | ch76aj | Flintshire | Sir Y Fflint | Mold WwTW | 3191 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 324635 | 366328 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6AZ | CH76AZ | ch7 6az | ch76az | Flintshire | Sir Y Fflint | Connahs Quay STW | 4389 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 326009 | 368220 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BG | CH76BG | ch7 6bg | ch76bg | Flintshire | Sir Y Fflint | Rhydymwyn STW | 3472 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 324318 | 367104 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BJ | CH76BJ | ch7 6bj | ch76bj | Flintshire | Sir Y Fflint | Mold WwTW | 3212 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324496 | 366341 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BX | CH76BX | ch7 6bx | ch76bx | Flintshire | Sir Y Fflint | Connahs Quay STW | 2393 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 327927 | 368771 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BY | CH76BY | ch7 6by | ch76by | Flintshire | Sir Y Fflint | Connahs Quay STW | 2596 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 327744 | 368670 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6BZ | CH76BZ | ch7 6bz | ch76bz | Flintshire | Sir Y Fflint | Connahs Quay STW | 2817 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 327562 | 368510 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DA | CH76DA | ch7 6da | ch76da | Flintshire | Sir Y Fflint | Mold WwTW | 3001 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324233 | 366095 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DE | CH76DE | ch7 6de | ch76de | Flintshire | Sir Y Fflint | Connahs Quay STW | 3954 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326545 | 367976 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DF | CH76DF | ch7 6df | ch76df | Flintshire | Sir Y Fflint | Connahs Quay STW | 3661 | 782 | 700to900 | 1.57 | 1.15 | 0.84 | 14.58 | 7.77 | 8.59 | 326582 | 369480 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DH | CH76DH | ch7 6dh | ch76dh | Flintshire | Sir Y Fflint | Connahs Quay STW | 4360 | 805 | 700to900 | 1.61 | 1.18 | 0.86 | 15 | 8 | 8.84 | 326063 | 368134 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DQ | CH76DQ | ch7 6dq | ch76dq | Flintshire | Sir Y Fflint | Connahs Quay STW | 2749 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 327510 | 369062 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DU | CH76DU | ch7 6du | ch76du | Flintshire | Sir Y Fflint | Mold WwTW | 3076 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 324651 | 366213 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DW | CH76DW | ch7 6dw | ch76dw | Flintshire | Sir Y Fflint | Connahs Quay STW | 3098 | 782 | 700to900 | 1.57 | 1.15 | 0.84 | 14.58 | 7.77 | 8.59 | 327144 | 369315 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DX | CH76DX | ch7 6dx | ch76dx | Flintshire | Sir Y Fflint | Mold WwTW | 3273 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 324728 | 366412 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DY | CH76DY | ch7 6dy | ch76dy | Flintshire | Sir Y Fflint | Mold WwTW | 3303 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 324636 | 366440 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6DZ | CH76DZ | ch7 6dz | ch76dz | Flintshire | Sir Y Fflint | Mold WwTW | 3244 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 324673 | 366382 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EA | CH76EA | ch7 6ea | ch76ea | Flintshire | Sir Y Fflint | Mold WwTW | 3145 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324217 | 366238 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EB | CH76EB | ch7 6eb | ch76eb | Flintshire | Sir Y Fflint | Mold WwTW | 3367 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324301 | 366476 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6ED | CH76ED | ch7 6ed | ch76ed | Flintshire | Sir Y Fflint | Mold WwTW | 3415 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 324342 | 366529 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EE | CH76EE | ch7 6ee | ch76ee | Flintshire | Sir Y Fflint | Mold WwTW | 3012 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324385 | 366129 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EF | CH76EF | ch7 6ef | ch76ef | Flintshire | Sir Y Fflint | Mold WwTW | 3059 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 324550 | 366191 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EG | CH76EG | ch7 6eg | ch76eg | Flintshire | Sir Y Fflint | Mold WwTW | 2953 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324245 | 366049 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EJ | CH76EJ | ch7 6ej | ch76ej | Flintshire | Sir Y Fflint | Mold WwTW | 3251 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 324598 | 366386 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EL | CH76EL | ch7 6el | ch76el | Flintshire | Sir Y Fflint | Mold WwTW | 3230 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324313 | 366339 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EN | CH76EN | ch7 6en | ch76en | Flintshire | Sir Y Fflint | Mold WwTW | 3135 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324276 | 366238 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EP | CH76EP | ch7 6ep | ch76ep | Flintshire | Sir Y Fflint | Connahs Quay STW | 2267 | 760 | 700to900 | 1.52 | 1.11 | 0.82 | 14.17 | 7.56 | 8.35 | 328053 | 368787 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EQ | CH76EQ | ch7 6eq | ch76eq | Flintshire | Sir Y Fflint | Mold WwTW | 2964 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324294 | 366068 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6ER | CH76ER | ch7 6er | ch76er | Flintshire | Sir Y Fflint | Mold WwTW | 3375 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 324568 | 366509 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6ES | CH76ES | ch7 6es | ch76es | Flintshire | Sir Y Fflint | Mold WwTW | 3858 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 326016 | 366783 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6ET | CH76ET | ch7 6et | ch76et | Flintshire | Sir Y Fflint | Mold WwTW | 3305 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 325159 | 366418 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EW | CH76EW | ch7 6ew | ch76ew | Flintshire | Sir Y Fflint | Mold WwTW | 3416 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 324635 | 366553 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EX | CH76EX | ch7 6ex | ch76ex | Flintshire | Sir Y Fflint | Mold WwTW | 3149 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324358 | 366263 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EY | CH76EY | ch7 6ey | ch76ey | Flintshire | Sir Y Fflint | Mold WwTW | 3232 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 324613 | 366368 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6EZ | CH76EZ | ch7 6ez | ch76ez | Flintshire | Sir Y Fflint | Mold WwTW | 3306 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 324793 | 366445 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6FB | CH76FB | ch7 6fb | ch76fb | Flintshire | Sir Y Fflint | Mold WwTW | 3028 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324421 | 366149 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6FD | CH76FD | ch7 6fd | ch76fd | Flintshire | Sir Y Fflint | Mold WwTW | 3131 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 324773 | 366270 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6FQ | CH76FQ | ch7 6fq | ch76fq | Flintshire | Sir Y Fflint | Mold WwTW | 894 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 324862 | 364027 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6FS | CH76FS | ch7 6fs | ch76fs | Flintshire | Sir Y Fflint | Mold WwTW | 3081 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 326976 | 365269 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6FT | CH76FT | ch7 6ft | ch76ft | Flintshire | Sir Y Fflint | Mold WwTW | 3079 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 326997 | 365243 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6FW | CH76FW | ch7 6fw | ch76fw | Flintshire | Sir Y Fflint | Mold WwTW | 2193 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325127 | 365300 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6FX | CH76FX | ch7 6fx | ch76fx | Flintshire | Sir Y Fflint | Mold WwTW | 2131 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326045 | 364831 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6FY | CH76FY | ch7 6fy | ch76fy | Flintshire | Sir Y Fflint | Mold WwTW | 2137 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326107 | 364790 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6FZ | CH76FZ | ch7 6fz | ch76fz | Flintshire | Sir Y Fflint | Mold WwTW | 2182 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326087 | 364864 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GA | CH76GA | ch7 6ga | ch76ga | Flintshire | Sir Y Fflint | Connahs Quay STW | 3219 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327410 | 367848 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GB | CH76GB | ch7 6gb | ch76gb | Flintshire | Sir Y Fflint | Connahs Quay STW | 3245 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327381 | 367847 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GD | CH76GD | ch7 6gd | ch76gd | Flintshire | Sir Y Fflint | Connahs Quay STW | 3218 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327361 | 367945 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GE | CH76GE | ch7 6ge | ch76ge | Flintshire | Sir Y Fflint | Connahs Quay STW | 3232 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327444 | 367760 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GF | CH76GF | ch7 6gf | ch76gf | Flintshire | Sir Y Fflint | Connahs Quay STW | 3467 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327140 | 367830 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GG | CH76GG | ch7 6gg | ch76gg | Flintshire | Sir Y Fflint | Mold WwTW | 2908 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324423 | 366029 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GH | CH76GH | ch7 6gh | ch76gh | Flintshire | Sir Y Fflint | Mold WwTW | 3088 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324476 | 366215 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GJ | CH76GJ | ch7 6gj | ch76gj | Flintshire | Sir Y Fflint | Connahs Quay STW | 3364 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327251 | 367839 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GL | CH76GL | ch7 6gl | ch76gl | Flintshire | Sir Y Fflint | Connahs Quay STW | 3419 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327204 | 367810 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GN | CH76GN | ch7 6gn | ch76gn | Flintshire | Sir Y Fflint | Connahs Quay STW | 3644 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326941 | 367835 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GT | CH76GT | ch7 6gt | ch76gt | Flintshire | Sir Y Fflint | Mold WwTW | 1917 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324125 | 364952 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GW | CH76GW | ch7 6gw | ch76gw | Flintshire | Sir Y Fflint | Mold WwTW | 1864 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324403 | 364971 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GX | CH76GX | ch7 6gx | ch76gx | Flintshire | Sir Y Fflint | Mold WwTW | 2184 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326053 | 364892 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6GY | CH76GY | ch7 6gy | ch76gy | Flintshire | Sir Y Fflint | Rhosesmor STW | 570 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 321472 | 368469 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HA | CH76HA | ch7 6ha | ch76ha | Flintshire | Sir Y Fflint | Mold WwTW | 2819 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324346 | 365929 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HB | CH76HB | ch7 6hb | ch76hb | Flintshire | Sir Y Fflint | Connahs Quay STW | 3666 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 327225 | 367297 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HE | CH76HE | ch7 6he | ch76he | Flintshire | Sir Y Fflint | Connahs Quay STW | 3727 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 327321 | 367064 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HF | CH76HF | ch7 6hf | ch76hf | Flintshire | Sir Y Fflint | Connahs Quay STW | 3620 | 804 | 700to900 | 1.61 | 1.18 | 0.86 | 14.99 | 7.99 | 8.83 | 327268 | 367315 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HG | CH76HG | ch7 6hg | ch76hg | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 3103 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327217 | 365248 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HH | CH76HH | ch7 6hh | ch76hh | Flintshire | Sir Y Fflint | Connahs Quay STW | 3887 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326838 | 367503 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HJ | CH76HJ | ch7 6hj | ch76hj | Flintshire | Sir Y Fflint | Connahs Quay STW | 3337 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 327594 | 367349 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HL | CH76HL | ch7 6hl | ch76hl | Flintshire | Sir Y Fflint | Connahs Quay STW | 3880 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326726 | 367738 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HN | CH76HN | ch7 6hn | ch76hn | Flintshire | Sir Y Fflint | Connahs Quay STW | 4008 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326691 | 367520 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HP | CH76HP | ch7 6hp | ch76hp | Flintshire | Sir Y Fflint | Connahs Quay STW | 3870 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326725 | 367765 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HR | CH76HR | ch7 6hr | ch76hr | Flintshire | Sir Y Fflint | Connahs Quay STW | 3864 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326685 | 367869 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HS | CH76HS | ch7 6hs | ch76hs | Flintshire | Sir Y Fflint | Connahs Quay STW | 3810 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326769 | 367811 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HT | CH76HT | ch7 6ht | ch76ht | Flintshire | Sir Y Fflint | Connahs Quay STW | 3330 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327355 | 367720 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HU | CH76HU | ch7 6hu | ch76hu | Flintshire | Sir Y Fflint | Connahs Quay STW | 3802 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326785 | 367797 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HW | CH76HW | ch7 6hw | ch76hw | Flintshire | Sir Y Fflint | Connahs Quay STW | 3889 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326740 | 367688 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HX | CH76HX | ch7 6hx | ch76hx | Flintshire | Sir Y Fflint | Connahs Quay STW | 3745 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326764 | 367991 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HY | CH76HY | ch7 6hy | ch76hy | Flintshire | Sir Y Fflint | Connahs Quay STW | 3657 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326890 | 367916 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6HZ | CH76HZ | ch7 6hz | ch76hz | Flintshire | Sir Y Fflint | Connahs Quay STW | 3711 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326799 | 367995 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JA | CH76JA | ch7 6ja | ch76ja | Flintshire | Sir Y Fflint | Connahs Quay STW | 3762 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326811 | 367836 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JB | CH76JB | ch7 6jb | ch76jb | Flintshire | Sir Y Fflint | Connahs Quay STW | 3756 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326833 | 367802 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JD | CH76JD | ch7 6jd | ch76jd | Flintshire | Sir Y Fflint | Connahs Quay STW | 3745 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326846 | 367801 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JE | CH76JE | ch7 6je | ch76je | Flintshire | Sir Y Fflint | Connahs Quay STW | 3726 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326868 | 367798 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JF | CH76JF | ch7 6jf | ch76jf | Flintshire | Sir Y Fflint | Connahs Quay STW | 3704 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326968 | 367646 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JG | CH76JG | ch7 6jg | ch76jg | Flintshire | Sir Y Fflint | Connahs Quay STW | 3482 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327151 | 367775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JH | CH76JH | ch7 6jh | ch76jh | Flintshire | Sir Y Fflint | Connahs Quay STW | 3517 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327146 | 367711 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JJ | CH76JJ | ch7 6jj | ch76jj | Flintshire | Sir Y Fflint | Connahs Quay STW | 3787 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326846 | 367704 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JL | CH76JL | ch7 6jl | ch76jl | Flintshire | Sir Y Fflint | Connahs Quay STW | 3353 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327349 | 367683 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JN | CH76JN | ch7 6jn | ch76jn | Flintshire | Sir Y Fflint | Connahs Quay STW | 3304 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327401 | 367692 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JP | CH76JP | ch7 6jp | ch76jp | Flintshire | Sir Y Fflint | Connahs Quay STW | 3262 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327452 | 367689 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JQ | CH76JQ | ch7 6jq | ch76jq | Flintshire | Sir Y Fflint | Connahs Quay STW | 3468 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327168 | 367773 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JR | CH76JR | ch7 6jr | ch76jr | Flintshire | Sir Y Fflint | Connahs Quay STW | 3805 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326723 | 367930 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JS | CH76JS | ch7 6js | ch76js | Flintshire | Sir Y Fflint | Connahs Quay STW | 3119 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 327575 | 367761 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JT | CH76JT | ch7 6jt | ch76jt | Flintshire | Sir Y Fflint | Connahs Quay STW | 3153 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327478 | 367862 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JU | CH76JU | ch7 6ju | ch76ju | Flintshire | Sir Y Fflint | Connahs Quay STW | 3552 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327059 | 367802 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JW | CH76JW | ch7 6jw | ch76jw | Flintshire | Sir Y Fflint | Connahs Quay STW | 3269 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327444 | 367688 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JX | CH76JX | ch7 6jx | ch76jx | Flintshire | Sir Y Fflint | Connahs Quay STW | 3793 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326760 | 367875 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JY | CH76JY | ch7 6jy | ch76jy | Flintshire | Sir Y Fflint | Connahs Quay STW | 3771 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326876 | 367679 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6JZ | CH76JZ | ch7 6jz | ch76jz | Flintshire | Sir Y Fflint | Connahs Quay STW | 3777 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326899 | 367620 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LA | CH76LA | ch7 6la | ch76la | Flintshire | Sir Y Fflint | Connahs Quay STW | 3400 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327332 | 367620 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LB | CH76LB | ch7 6lb | ch76lb | Flintshire | Sir Y Fflint | Connahs Quay STW | 3138 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 327595 | 367694 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LD | CH76LD | ch7 6ld | ch76ld | Flintshire | Sir Y Fflint | Connahs Quay STW | 2964 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 327779 | 367729 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LE | CH76LE | ch7 6le | ch76le | Flintshire | Sir Y Fflint | Connahs Quay STW | 3055 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 327777 | 367574 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LF | CH76LF | ch7 6lf | ch76lf | Flintshire | Sir Y Fflint | Connahs Quay STW | 3093 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 327754 | 367542 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LG | CH76LG | ch7 6lg | ch76lg | Flintshire | Sir Y Fflint | Mold WwTW | 3620 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 327072 | 365916 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LH | CH76LH | ch7 6lh | ch76lh | Flintshire | Sir Y Fflint | Mold WwTW | 2871 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326439 | 365461 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LJ | CH76LJ | ch7 6lj | ch76lj | Flintshire | Sir Y Fflint | Connahs Quay STW | 3106 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 327626 | 367705 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LL | CH76LL | ch7 6ll | ch76ll | Flintshire | Sir Y Fflint | Connahs Quay STW | 3291 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327459 | 367622 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LN | CH76LN | ch7 6ln | ch76ln | Flintshire | Sir Y Fflint | Connahs Quay STW | 3325 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327435 | 367597 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LP | CH76LP | ch7 6lp | ch76lp | Flintshire | Sir Y Fflint | Connahs Quay STW | 3258 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 327523 | 367584 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LQ | CH76LQ | ch7 6lq | ch76lq | Flintshire | Sir Y Fflint | Mold WwTW | 2649 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326093 | 365422 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LR | CH76LR | ch7 6lr | ch76lr | Flintshire | Sir Y Fflint | Mold WwTW | 2854 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 323988 | 365889 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LU | CH76LU | ch7 6lu | ch76lu | Flintshire | Sir Y Fflint | Mold WwTW | 2573 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 323098 | 365112 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LW | CH76LW | ch7 6lw | ch76lw | Flintshire | Sir Y Fflint | Connahs Quay STW | 3206 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 327578 | 367595 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LX | CH76LX | ch7 6lx | ch76lx | Flintshire | Sir Y Fflint | Rhydymwyn STW | 2355 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 322935 | 365316 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6LZ | CH76LZ | ch7 6lz | ch76lz | Flintshire | Sir Y Fflint | Rhydymwyn STW | 2422 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 322983 | 365266 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NA | CH76NA | ch7 6na | ch76na | Flintshire | Sir Y Fflint | Mold WwTW | 1943 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324121 | 364978 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NB | CH76NB | ch7 6nb | ch76nb | Flintshire | Sir Y Fflint | Mold WwTW | 1943 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324121 | 364978 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6ND | CH76ND | ch7 6nd | ch76nd | Flintshire | Sir Y Fflint | Mold WwTW | 1943 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324121 | 364978 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NE | CH76NE | ch7 6ne | ch76ne | Flintshire | Sir Y Fflint | Mold WwTW | 1848 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326196 | 364290 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NF | CH76NF | ch7 6nf | ch76nf | Flintshire | Sir Y Fflint | Mold WwTW | 1917 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324125 | 364952 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NG | CH76NG | ch7 6ng | ch76ng | Flintshire | Sir Y Fflint | Mold WwTW | 1943 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324121 | 364978 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NH | CH76NH | ch7 6nh | ch76nh | Flintshire | Sir Y Fflint | Mold WwTW | 2259 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326273 | 364808 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NJ | CH76NJ | ch7 6nj | ch76nj | Flintshire | Sir Y Fflint | Mold WwTW | 1803 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326148 | 364277 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NL | CH76NL | ch7 6nl | ch76nl | Flintshire | Sir Y Fflint | Mold WwTW | 2186 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326200 | 364775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NN | CH76NN | ch7 6nn | ch76nn | Flintshire | Sir Y Fflint | Mold WwTW | 1943 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324121 | 364978 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NP | CH76NP | ch7 6np | ch76np | Flintshire | Sir Y Fflint | Connahs Quay STW | 3220 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 327583 | 367563 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NQ | CH76NQ | ch7 6nq | ch76nq | Flintshire | Sir Y Fflint | Connahs Quay STW | 3651 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327007 | 367686 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NR | CH76NR | ch7 6nr | ch76nr | Flintshire | Sir Y Fflint | Mold WwTW | 1943 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324121 | 364978 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NS | CH76NS | ch7 6ns | ch76ns | Flintshire | Sir Y Fflint | Connahs Quay STW | 3535 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327167 | 367635 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NT | CH76NT | ch7 6nt | ch76nt | Flintshire | Sir Y Fflint | Mold WwTW | 1943 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324121 | 364978 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NU | CH76NU | ch7 6nu | ch76nu | Flintshire | Sir Y Fflint | Connahs Quay STW | 3558 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327135 | 367645 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NW | CH76NW | ch7 6nw | ch76nw | Flintshire | Sir Y Fflint | Mold WwTW | 2120 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324074 | 365149 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NX | CH76NX | ch7 6nx | ch76nx | Flintshire | Sir Y Fflint | Connahs Quay STW | 3473 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 327202 | 367699 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NY | CH76NY | ch7 6ny | ch76ny | Flintshire | Sir Y Fflint | Connahs Quay STW | 3708 | 795 | 700to900 | 1.59 | 1.16 | 0.85 | 14.82 | 7.9 | 8.73 | 327550 | 366829 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6NZ | CH76NZ | ch7 6nz | ch76nz | Flintshire | Sir Y Fflint | Mold WwTW | 4151 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 327353 | 366372 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PA | CH76PA | ch7 6pa | ch76pa | Flintshire | Sir Y Fflint | Rhydymwyn STW | 1871 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322770 | 366453 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PB | CH76PB | ch7 6pb | ch76pb | Flintshire | Sir Y Fflint | Rhydymwyn STW | 1656 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 322552 | 366396 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PD | CH76PD | ch7 6pd | ch76pd | Flintshire | Sir Y Fflint | Rhydymwyn STW | 740 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 321639 | 366541 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PE | CH76PE | ch7 6pe | ch76pe | Flintshire | Sir Y Fflint | Rhydymwyn STW | 738 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 321585 | 366773 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PF | CH76PF | ch7 6pf | ch76pf | Flintshire | Sir Y Fflint | Rhosesmor STW | 307 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 321251 | 367974 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PG | CH76PG | ch7 6pg | ch76pg | Flintshire | Sir Y Fflint | Rhosesmor STW | 1255 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 322061 | 367480 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PH | CH76PH | ch7 6ph | ch76ph | Flintshire | Sir Y Fflint | Rhosesmor STW | 565 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 321500 | 368413 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PL | CH76PL | ch7 6pl | ch76pl | Flintshire | Sir Y Fflint | Rhosesmor STW | 214 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 321214 | 368157 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PN | CH76PN | ch7 6pn | ch76pn | Flintshire | Sir Y Fflint | Rhosesmor STW | 528 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 321379 | 368518 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PQ | CH76PQ | ch7 6pq | ch76pq | Flintshire | Sir Y Fflint | Rhosesmor STW | 638 | 907 | 900to1200 | 1.82 | 1.33 | 0.97 | 16.91 | 9.02 | 9.97 | 321584 | 368406 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PW | CH76PW | ch7 6pw | ch76pw | Flintshire | Sir Y Fflint | Rhosesmor STW | 501 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 321303 | 368549 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PY | CH76PY | ch7 6py | ch76py | Flintshire | Sir Y Fflint | Rhosesmor STW | 828 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 320526 | 368828 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6PZ | CH76PZ | ch7 6pz | ch76pz | Flintshire | Sir Y Fflint | Rhosesmor STW | 287 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 321287 | 368164 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QA | CH76QA | ch7 6qa | ch76qa | Flintshire | Sir Y Fflint | Mold WwTW | 2114 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325193 | 365206 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QB | CH76QB | ch7 6qb | ch76qb | Flintshire | Sir Y Fflint | Rhosesmor STW | 477 | 926 | 900to1200 | 1.85 | 1.36 | 0.99 | 17.26 | 9.2 | 10.17 | 321304 | 368517 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QD | CH76QD | ch7 6qd | ch76qd | Flintshire | Sir Y Fflint | Rhosesmor STW | 403 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 321296 | 368423 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QE | CH76QE | ch7 6qe | ch76qe | Flintshire | Sir Y Fflint | Rhosesmor STW | 455 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 321362 | 368425 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QG | CH76QG | ch7 6qg | ch76qg | Flintshire | Sir Y Fflint | Mold WwTW | 1861 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324341 | 364955 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QJ | CH76QJ | ch7 6qj | ch76qj | Flintshire | Sir Y Fflint | Mold WwTW | 2386 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325105 | 365499 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QL | CH76QL | ch7 6ql | ch76ql | Flintshire | Sir Y Fflint | Mold WwTW | 2228 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325166 | 365328 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QN | CH76QN | ch7 6qn | ch76qn | Flintshire | Sir Y Fflint | Mold WwTW | 2254 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325297 | 365326 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QP | CH76QP | ch7 6qp | ch76qp | Flintshire | Sir Y Fflint | Mold WwTW | 2334 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325238 | 365422 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QQ | CH76QQ | ch7 6qq | ch76qq | Flintshire | Sir Y Fflint | Mold WwTW | 2276 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325102 | 365388 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QR | CH76QR | ch7 6qr | ch76qr | Flintshire | Sir Y Fflint | Mold WwTW | 2358 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325279 | 365437 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QS | CH76QS | ch7 6qs | ch76qs | Flintshire | Sir Y Fflint | Mold WwTW | 2366 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325294 | 365442 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QT | CH76QT | ch7 6qt | ch76qt | Flintshire | Sir Y Fflint | Mold WwTW | 2378 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325332 | 365445 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QU | CH76QU | ch7 6qu | ch76qu | Flintshire | Sir Y Fflint | Mold WwTW | 2090 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325328 | 365148 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QW | CH76QW | ch7 6qw | ch76qw | Flintshire | Sir Y Fflint | Mold WwTW | 2370 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325305 | 365443 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QX | CH76QX | ch7 6qx | ch76qx | Flintshire | Sir Y Fflint | Mold WwTW | 2128 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325348 | 365182 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QY | CH76QY | ch7 6qy | ch76qy | Flintshire | Sir Y Fflint | Mold WwTW | 2115 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325413 | 365148 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6QZ | CH76QZ | ch7 6qz | ch76qz | Flintshire | Sir Y Fflint | Mold WwTW | 1717 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324226 | 364775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RA | CH76RA | ch7 6ra | ch76ra | Flintshire | Sir Y Fflint | Mold WwTW | 2061 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326002 | 364776 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RB | CH76RB | ch7 6rb | ch76rb | Flintshire | Sir Y Fflint | Mold WwTW | 2542 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 325127 | 365653 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RD | CH76RD | ch7 6rd | ch76rd | Flintshire | Sir Y Fflint | Mold WwTW | 2342 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325414 | 365385 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RE | CH76RE | ch7 6re | ch76re | Flintshire | Sir Y Fflint | Mold WwTW | 1830 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326496 | 363686 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RF | CH76RF | ch7 6rf | ch76rf | Flintshire | Sir Y Fflint | Mold WwTW | 2351 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325519 | 365361 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RG | CH76RG | ch7 6rg | ch76rg | Flintshire | Sir Y Fflint | Mold WwTW | 2208 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325382 | 365255 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RH | CH76RH | ch7 6rh | ch76rh | Flintshire | Sir Y Fflint | Mold WwTW | 3168 | 826 | 700to900 | 1.65 | 1.21 | 0.89 | 15.4 | 8.21 | 9.08 | 325574 | 366198 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RJ | CH76RJ | ch7 6rj | ch76rj | Flintshire | Sir Y Fflint | Mold WwTW | 3200 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 326619 | 365736 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RL | CH76RL | ch7 6rl | ch76rl | Flintshire | Sir Y Fflint | Mold WwTW | 3068 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 326639 | 365556 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RN | CH76RN | ch7 6rn | ch76rn | Flintshire | Sir Y Fflint | Mold WwTW | 3283 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 326823 | 365684 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RP | CH76RP | ch7 6rp | ch76rp | Flintshire | Sir Y Fflint | Mold WwTW | 2917 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324033 | 365967 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RQ | CH76RQ | ch7 6rq | ch76rq | Flintshire | Sir Y Fflint | Mold WwTW | 2750 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 325353 | 365822 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RR | CH76RR | ch7 6rr | ch76rr | Flintshire | Sir Y Fflint | Mold WwTW | 3112 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 324639 | 366249 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RT | CH76RT | ch7 6rt | ch76rt | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2695 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327239 | 364834 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RU | CH76RU | ch7 6ru | ch76ru | Flintshire | Sir Y Fflint | Mold WwTW | 2183 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325516 | 365183 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RW | CH76RW | ch7 6rw | ch76rw | Flintshire | Sir Y Fflint | Mold WwTW | 3092 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 326957 | 365304 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RX | CH76RX | ch7 6rx | ch76rx | Flintshire | Sir Y Fflint | Mold WwTW | 2230 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325461 | 365253 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RY | CH76RY | ch7 6ry | ch76ry | Flintshire | Sir Y Fflint | Mold WwTW | 2003 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325925 | 364761 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6RZ | CH76RZ | ch7 6rz | ch76rz | Flintshire | Sir Y Fflint | Mold WwTW | 1990 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326136 | 364567 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SA | CH76SA | ch7 6sa | ch76sa | Flintshire | Sir Y Fflint | Mold WwTW | 1726 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326373 | 363727 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SB | CH76SB | ch7 6sb | ch76sb | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2809 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327006 | 364885 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SD | CH76SD | ch7 6sd | ch76sd | Flintshire | Sir Y Fflint | Mold WwTW | 1712 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326350 | 363747 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SE | CH76SE | ch7 6se | ch76se | Flintshire | Sir Y Fflint | Mold WwTW | 2004 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325844 | 364818 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SF | CH76SF | ch7 6sf | ch76sf | Flintshire | Sir Y Fflint | Mold WwTW | 1892 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325770 | 364733 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SG | CH76SG | ch7 6sg | ch76sg | Flintshire | Sir Y Fflint | Mold WwTW | 2072 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325947 | 364831 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SH | CH76SH | ch7 6sh | ch76sh | Flintshire | Sir Y Fflint | Mold WwTW | 2061 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326129 | 364671 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SJ | CH76SJ | ch7 6sj | ch76sj | Flintshire | Sir Y Fflint | Mold WwTW | 1824 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325813 | 364621 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SL | CH76SL | ch7 6sl | ch76sl | Flintshire | Sir Y Fflint | Mold WwTW | 1897 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325866 | 364673 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SN | CH76SN | ch7 6sn | ch76sn | Flintshire | Sir Y Fflint | Mold WwTW | 1959 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326039 | 364614 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SP | CH76SP | ch7 6sp | ch76sp | Flintshire | Sir Y Fflint | Mold WwTW | 1977 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326148 | 364537 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SQ | CH76SQ | ch7 6sq | ch76sq | Flintshire | Sir Y Fflint | Mold WwTW | 1456 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 325419 | 364433 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SR | CH76SR | ch7 6sr | ch76sr | Flintshire | Sir Y Fflint | Mold WwTW | 3340 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324363 | 366456 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SS | CH76SS | ch7 6ss | ch76ss | Flintshire | Sir Y Fflint | Mold WwTW | 3459 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 324514 | 366590 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6ST | CH76ST | ch7 6st | ch76st | Flintshire | Sir Y Fflint | Mold WwTW | 3419 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 324560 | 366553 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SU | CH76SU | ch7 6su | ch76su | Flintshire | Sir Y Fflint | Mold WwTW | 3272 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324344 | 366386 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SW | CH76SW | ch7 6sw | ch76sw | Flintshire | Sir Y Fflint | Mold WwTW | 1952 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326073 | 364575 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SX | CH76SX | ch7 6sx | ch76sx | Flintshire | Sir Y Fflint | Mold WwTW | 3221 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324390 | 366340 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SY | CH76SY | ch7 6sy | ch76sy | Flintshire | Sir Y Fflint | Mold WwTW | 3190 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324438 | 366314 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6SZ | CH76SZ | ch7 6sz | ch76sz | Flintshire | Sir Y Fflint | Mold WwTW | 2014 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326217 | 364519 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TA | CH76TA | ch7 6ta | ch76ta | Flintshire | Sir Y Fflint | Mold WwTW | 579 | 864 | 700to900 | 1.73 | 1.27 | 0.93 | 16.1 | 8.59 | 9.49 | 325317 | 363254 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TB | CH76TB | ch7 6tb | ch76tb | Flintshire | Sir Y Fflint | Mold WwTW | 1779 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326435 | 363708 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TD | CH76TD | ch7 6td | ch76td | Flintshire | Sir Y Fflint | Mold WwTW | 1597 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326185 | 363840 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TE | CH76TE | ch7 6te | ch76te | Flintshire | Sir Y Fflint | Mold WwTW | 1644 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326209 | 363897 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TF | CH76TF | ch7 6tf | ch76tf | Flintshire | Sir Y Fflint | Mold WwTW | 1106 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325632 | 363806 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TG | CH76TG | ch7 6tg | ch76tg | Flintshire | Sir Y Fflint | Mold WwTW | 1074 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325539 | 363868 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TH | CH76TH | ch7 6th | ch76th | Flintshire | Sir Y Fflint | Mold WwTW | 1589 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326188 | 363814 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TJ | CH76TJ | ch7 6tj | ch76tj | Flintshire | Sir Y Fflint | Mold WwTW | 1734 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325961 | 364380 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TL | CH76TL | ch7 6tl | ch76tl | Flintshire | Sir Y Fflint | Mold WwTW | 1800 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326074 | 364359 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TN | CH76TN | ch7 6tn | ch76tn | Flintshire | Sir Y Fflint | Mold WwTW | 1980 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326222 | 364464 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TP | CH76TP | ch7 6tp | ch76tp | Flintshire | Sir Y Fflint | Mold WwTW | 1919 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326242 | 364346 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TQ | CH76TQ | ch7 6tq | ch76tq | Flintshire | Sir Y Fflint | Mold WwTW | 1898 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326444 | 363995 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TR | CH76TR | ch7 6tr | ch76tr | Flintshire | Sir Y Fflint | Mold WwTW | 1862 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326073 | 364450 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TS | CH76TS | ch7 6ts | ch76ts | Flintshire | Sir Y Fflint | Mold WwTW | 1090 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325558 | 363871 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TT | CH76TT | ch7 6tt | ch76tt | Flintshire | Sir Y Fflint | Mold WwTW | 875 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 325338 | 363788 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TU | CH76TU | ch7 6tu | ch76tu | Flintshire | Sir Y Fflint | Mold WwTW | 2901 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324328 | 366009 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TW | CH76TW | ch7 6tw | ch76tw | Flintshire | Sir Y Fflint | Mold WwTW | 1949 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326290 | 364334 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TX | CH76TX | ch7 6tx | ch76tx | Flintshire | Sir Y Fflint | Mold WwTW | 1148 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 325488 | 364019 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TY | CH76TY | ch7 6ty | ch76ty | Flintshire | Sir Y Fflint | Mold WwTW | 1853 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326145 | 364359 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6TZ | CH76TZ | ch7 6tz | ch76tz | Flintshire | Sir Y Fflint | Mold WwTW | 1820 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326079 | 364383 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UA | CH76UA | ch7 6ua | ch76ua | Flintshire | Sir Y Fflint | Mold WwTW | 1368 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326008 | 363676 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UB | CH76UB | ch7 6ub | ch76ub | Flintshire | Sir Y Fflint | Mold WwTW | 1448 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325799 | 364138 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UD | CH76UD | ch7 6ud | ch76ud | Flintshire | Sir Y Fflint | Mold WwTW | 1437 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325770 | 364151 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UE | CH76UE | ch7 6ue | ch76ue | Flintshire | Sir Y Fflint | Mold WwTW | 1302 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325724 | 364004 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UF | CH76UF | ch7 6uf | ch76uf | Flintshire | Sir Y Fflint | Mold WwTW | 1392 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325882 | 363950 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UG | CH76UG | ch7 6ug | ch76ug | Flintshire | Sir Y Fflint | Mold WwTW | 1282 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325794 | 363883 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UH | CH76UH | ch7 6uh | ch76uh | Flintshire | Sir Y Fflint | Mold WwTW | 1544 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325966 | 364091 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UJ | CH76UJ | ch7 6uj | ch76uj | Flintshire | Sir Y Fflint | Mold WwTW | 1563 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326082 | 363957 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UL | CH76UL | ch7 6ul | ch76ul | Flintshire | Sir Y Fflint | Mold WwTW | 1610 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326018 | 364131 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UN | CH76UN | ch7 6un | ch76un | Flintshire | Sir Y Fflint | Mold WwTW | 1675 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325900 | 364357 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UP | CH76UP | ch7 6up | ch76up | Flintshire | Sir Y Fflint | Mold WwTW | 1435 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325891 | 364010 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UQ | CH76UQ | ch7 6uq | ch76uq | Flintshire | Sir Y Fflint | Mold WwTW | 1389 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325919 | 363890 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UR | CH76UR | ch7 6ur | ch76ur | Flintshire | Sir Y Fflint | Mold WwTW | 1398 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325798 | 364064 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6US | CH76US | ch7 6us | ch76us | Flintshire | Sir Y Fflint | Mold WwTW | 1583 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326222 | 363722 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UT | CH76UT | ch7 6ut | ch76ut | Flintshire | Sir Y Fflint | Mold WwTW | 1546 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326153 | 363787 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UU | CH76UU | ch7 6uu | ch76uu | Flintshire | Sir Y Fflint | Mold WwTW | 1766 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326317 | 363953 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UW | CH76UW | ch7 6uw | ch76uw | Flintshire | Sir Y Fflint | Mold WwTW | 1679 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325951 | 364313 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UX | CH76UX | ch7 6ux | ch76ux | Flintshire | Sir Y Fflint | Mold WwTW | 1869 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326423 | 363972 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UY | CH76UY | ch7 6uy | ch76uy | Flintshire | Sir Y Fflint | Mold WwTW | 1481 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325899 | 364074 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6UZ | CH76UZ | ch7 6uz | ch76uz | Flintshire | Sir Y Fflint | Mold WwTW | 1643 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325791 | 364410 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WA | CH76WA | ch7 6wa | ch76wa | Flintshire | Sir Y Fflint | Rhosesmor STW | 4082 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 325064 | 367777 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WB | CH76WB | ch7 6wb | ch76wb | Flintshire | Sir Y Fflint | Mold WwTW | 1532 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 326266 | 362925 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WD | CH76WD | ch7 6wd | ch76wd | Flintshire | Sir Y Fflint | Mold WwTW | 4229 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 325392 | 367319 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WE | CH76WE | ch7 6we | ch76we | Flintshire | Sir Y Fflint | Mold WwTW | 2346 | 849 | 700to900 | 1.7 | 1.24 | 0.91 | 15.82 | 8.44 | 9.33 | 325034 | 365468 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WG | CH76WG | ch7 6wg | ch76wg | Flintshire | Sir Y Fflint | Mold WwTW | 1583 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326135 | 363906 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WH | CH76WH | ch7 6wh | ch76wh | Flintshire | Sir Y Fflint | Mold WwTW | 3484 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 324654 | 366622 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WL | CH76WL | ch7 6wl | ch76wl | Flintshire | Sir Y Fflint | Mold WwTW | 2157 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326179 | 364755 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WN | CH76WN | ch7 6wn | ch76wn | Flintshire | Sir Y Fflint | Mold WwTW | 3540 | 829 | 700to900 | 1.66 | 1.21 | 0.89 | 15.45 | 8.24 | 9.11 | 324618 | 366676 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WT | CH76WT | ch7 6wt | ch76wt | Flintshire | Sir Y Fflint | Mold WwTW | 2069 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 326071 | 364731 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WU | CH76WU | ch7 6wu | ch76wu | Flintshire | Sir Y Fflint | Ty Gwyn WwTW | 2708 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 327264 | 364854 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6WZ | CH76WZ | ch7 6wz | ch76wz | Flintshire | Sir Y Fflint | Mold WwTW | 1643 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326251 | 363808 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XA | CH76XA | ch7 6xa | ch76xa | Flintshire | Sir Y Fflint | Mold WwTW | 1484 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325673 | 364302 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XB | CH76XB | ch7 6xb | ch76xb | Flintshire | Sir Y Fflint | Mold WwTW | 1559 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325731 | 364351 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XD | CH76XD | ch7 6xd | ch76xd | Flintshire | Sir Y Fflint | Mold WwTW | 1678 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325638 | 364563 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XE | CH76XE | ch7 6xe | ch76xe | Flintshire | Sir Y Fflint | Mold WwTW | 1483 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325642 | 364324 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XF | CH76XF | ch7 6xf | ch76xf | Flintshire | Sir Y Fflint | Mold WwTW | 1401 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325569 | 364276 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XG | CH76XG | ch7 6xg | ch76xg | Flintshire | Sir Y Fflint | Mold WwTW | 1453 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325575 | 364335 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XH | CH76XH | ch7 6xh | ch76xh | Flintshire | Sir Y Fflint | Mold WwTW | 1692 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325685 | 364549 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XJ | CH76XJ | ch7 6xj | ch76xj | Flintshire | Sir Y Fflint | Mold WwTW | 1167 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325630 | 363906 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XL | CH76XL | ch7 6xl | ch76xl | Flintshire | Sir Y Fflint | Mold WwTW | 1120 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325551 | 363922 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XN | CH76XN | ch7 6xn | ch76xn | Flintshire | Sir Y Fflint | Mold WwTW | 1062 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 325483 | 363908 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XP | CH76XP | ch7 6xp | ch76xp | Flintshire | Sir Y Fflint | Mold WwTW | 1758 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325726 | 364602 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XQ | CH76XQ | ch7 6xq | ch76xq | Flintshire | Sir Y Fflint | Mold WwTW | 1565 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325592 | 364459 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XR | CH76XR | ch7 6xr | ch76xr | Flintshire | Sir Y Fflint | Mold WwTW | 1712 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326156 | 364115 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XS | CH76XS | ch7 6xs | ch76xs | Flintshire | Sir Y Fflint | Mold WwTW | 1735 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326196 | 364098 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XT | CH76XT | ch7 6xt | ch76xt | Flintshire | Sir Y Fflint | Mold WwTW | 1629 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326083 | 364075 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XU | CH76XU | ch7 6xu | ch76xu | Flintshire | Sir Y Fflint | Mold WwTW | 1689 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326195 | 364014 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XW | CH76XW | ch7 6xw | ch76xw | Flintshire | Sir Y Fflint | Mold WwTW | 1785 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325758 | 364613 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XX | CH76XX | ch7 6xx | ch76xx | Flintshire | Sir Y Fflint | Mold WwTW | 1763 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326258 | 364053 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XY | CH76XY | ch7 6xy | ch76xy | Flintshire | Sir Y Fflint | Mold WwTW | 1928 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326409 | 364121 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6XZ | CH76XZ | ch7 6xz | ch76xz | Flintshire | Sir Y Fflint | Mold WwTW | 1830 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326312 | 364092 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YA | CH76YA | ch7 6ya | ch76ya | Flintshire | Sir Y Fflint | Mold WwTW | 1951 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326362 | 364238 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YB | CH76YB | ch7 6yb | ch76yb | Flintshire | Sir Y Fflint | Mold WwTW | 1900 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 326369 | 364133 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YD | CH76YD | ch7 6yd | ch76yd | Flintshire | Sir Y Fflint | Mold WwTW | 1778 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325595 | 364704 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YE | CH76YE | ch7 6ye | ch76ye | Flintshire | Sir Y Fflint | Mold WwTW | 1711 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325551 | 364651 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YF | CH76YF | ch7 6yf | ch76yf | Flintshire | Sir Y Fflint | Mold WwTW | 1014 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 325376 | 363937 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YG | CH76YG | ch7 6yg | ch76yg | Flintshire | Sir Y Fflint | Mold WwTW | 953 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 325289 | 363926 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YH | CH76YH | ch7 6yh | ch76yh | Flintshire | Sir Y Fflint | Mold WwTW | 1120 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 325420 | 364037 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YJ | CH76YJ | ch7 6yj | ch76yj | Flintshire | Sir Y Fflint | Connahs Quay STW | 3864 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326661 | 367927 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YL | CH76YL | ch7 6yl | ch76yl | Flintshire | Sir Y Fflint | Mold WwTW | 1219 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325564 | 364047 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YN | CH76YN | ch7 6yn | ch76yn | Flintshire | Sir Y Fflint | Mold WwTW | 1267 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325655 | 364026 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YP | CH76YP | ch7 6yp | ch76yp | Flintshire | Sir Y Fflint | Mold WwTW | 1313 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325606 | 364135 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YQ | CH76YQ | ch7 6yq | ch76yq | Flintshire | Sir Y Fflint | Mold WwTW | 1139 | 861 | 700to900 | 1.72 | 1.26 | 0.92 | 16.05 | 8.56 | 9.46 | 325399 | 364075 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YR | CH76YR | ch7 6yr | ch76yr | Flintshire | Sir Y Fflint | Mold WwTW | 1424 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325733 | 364170 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YS | CH76YS | ch7 6ys | ch76ys | Flintshire | Sir Y Fflint | Mold WwTW | 1589 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325652 | 364447 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YT | CH76YT | ch7 6yt | ch76yt | Flintshire | Sir Y Fflint | Mold WwTW | 3296 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324385 | 366415 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YW | CH76YW | ch7 6yw | ch76yw | Flintshire | Sir Y Fflint | Mold WwTW | 1211 | 851 | 700to900 | 1.7 | 1.25 | 0.91 | 15.86 | 8.46 | 9.35 | 325631 | 363970 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YX | CH76YX | ch7 6yx | ch76yx | Flintshire | Sir Y Fflint | Connahs Quay STW | 3916 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 326598 | 367945 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6YY | CH76YY | ch7 6yy | ch76yy | Flintshire | Sir Y Fflint | Mold WwTW | 3081 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 324340 | 366193 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6ZA | CH76ZA | ch7 6za | ch76za | Flintshire | Sir Y Fflint | Mold WwTW | 2471 | 843 | 700to900 | 1.69 | 1.23 | 0.91 | 15.71 | 8.38 | 9.26 | 325342 | 365538 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6ZB | CH76ZB | ch7 6zb | ch76zb | Flintshire | Sir Y Fflint | Mold WwTW | 1874 | 836 | 700to900 | 1.67 | 1.22 | 0.9 | 15.58 | 8.31 | 9.19 | 325632 | 364793 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 6ZG | CH76ZG | ch7 6zg | ch76zg | Flintshire | Sir Y Fflint | Mold WwTW | 1943 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324121 | 364978 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9AU | CH79AU | ch7 9au | ch79au | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9BQ | CH79BQ | ch7 9bq | ch79bq | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9DH | CH79DH | ch7 9dh | ch79dh | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9EH | CH79EH | ch7 9eh | ch79eh | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9EQ | CH79EQ | ch7 9eq | ch79eq | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9EU | CH79EU | ch7 9eu | ch79eu | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9EY | CH79EY | ch7 9ey | ch79ey | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9EZ | CH79EZ | ch7 9ez | ch79ez | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9FJ | CH79FJ | ch7 9fj | ch79fj | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9FQ | CH79FQ | ch7 9fq | ch79fq | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9FU | CH79FU | ch7 9fu | ch79fu | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9FW | CH79FW | ch7 9fw | ch79fw | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9FX | CH79FX | ch7 9fx | ch79fx | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9FY | CH79FY | ch7 9fy | ch79fy | Flintshire | Sir Y Fflint | Mold WwTW | 1412 | 880 | 700to900 | 1.76 | 1.29 | 0.95 | 16.4 | 8.75 | 9.67 | 323621 | 363987 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9XA | CH79XA | ch7 9xa | ch79xa | Flintshire | Sir Y Fflint | Mold WwTW | 1943 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324121 | 364978 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9ZY | CH79ZY | ch7 9zy | ch79zy | Flintshire | Sir Y Fflint | Mold WwTW | 1943 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324121 | 364978 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
CH7 9ZZ | CH79ZZ | ch7 9zz | ch79zz | Flintshire | Sir Y Fflint | Mold WwTW | 1943 | 879 | 700to900 | 1.76 | 1.29 | 0.94 | 16.38 | 8.74 | 9.66 | 324121 | 364978 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 0EW | LL110EW | ll11 0ew | ll110ew | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0FB | LL110FB | ll11 0fb | ll110fb | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0FS | LL110FS | ll11 0fs | ll110fs | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0FT | LL110FT | ll11 0ft | ll110ft | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0GW | LL110GW | ll11 0gw | ll110gw | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0HJ | LL110HJ | ll11 0hj | ll110hj | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0JJ | LL110JJ | ll11 0jj | ll110jj | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0JW | LL110JW | ll11 0jw | ll110jw | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0LG | LL110LG | ll11 0lg | ll110lg | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0LR | LL110LR | ll11 0lr | ll110lr | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0LS | LL110LS | ll11 0ls | ll110ls | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0NH | LL110NH | ll11 0nh | ll110nh | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0NN | LL110NN | ll11 0nn | ll110nn | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0NP | LL110NP | ll11 0np | ll110np | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0NQ | LL110NQ | ll11 0nq | ll110nq | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0NR | LL110NR | ll11 0nr | ll110nr | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0PF | LL110PF | ll11 0pf | ll110pf | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0PH | LL110PH | ll11 0ph | ll110ph | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0PN | LL110PN | ll11 0pn | ll110pn | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0PR | LL110PR | ll11 0pr | ll110pr | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0PU | LL110PU | ll11 0pu | ll110pu | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0QD | LL110QD | ll11 0qd | ll110qd | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0QP | LL110QP | ll11 0qp | ll110qp | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0QQ | LL110QQ | ll11 0qq | ll110qq | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0QX | LL110QX | ll11 0qx | ll110qx | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0RA | LL110RA | ll11 0ra | ll110ra | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0RE | LL110RE | ll11 0re | ll110re | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0RF | LL110RF | ll11 0rf | ll110rf | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0RH | LL110RH | ll11 0rh | ll110rh | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0RJ | LL110RJ | ll11 0rj | ll110rj | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0RL | LL110RL | ll11 0rl | ll110rl | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0RN | LL110RN | ll11 0rn | ll110rn | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0RQ | LL110RQ | ll11 0rq | ll110rq | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0ZX | LL110ZX | ll11 0zx | ll110zx | Wrexham | Wrecsam | Abenbury WwTW | 3819 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333433 | 350601 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0ZY | LL110ZY | ll11 0zy | ll110zy | Wrexham | Wrecsam | Abenbury WwTW | 3722 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333471 | 350486 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 0ZZ | LL110ZZ | ll11 0zz | ll110zz | Wrexham | Wrecsam | Abenbury WwTW | 3722 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333471 | 350486 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1AA | LL111AA | ll11 1aa | ll111aa | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1AB | LL111AB | ll11 1ab | ll111ab | Wrexham | Wrecsam | Abenbury WwTW | 3606 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333527 | 350360 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1AF | LL111AF | ll11 1af | ll111af | Wrexham | Wrecsam | Abenbury WwTW | 3569 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333514 | 350271 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1AG | LL111AG | ll11 1ag | ll111ag | Wrexham | Wrecsam | Abenbury WwTW | 3530 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333548 | 350251 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1AH | LL111AH | ll11 1ah | ll111ah | Wrexham | Wrecsam | Abenbury WwTW | 3550 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333544 | 350282 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1AL | LL111AL | ll11 1al | ll111al | Wrexham | Wrecsam | Abenbury WwTW | 3607 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333499 | 350318 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1AP | LL111AP | ll11 1ap | ll111ap | Wrexham | Wrecsam | Abenbury WwTW | 3650 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333475 | 350360 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1AR | LL111AR | ll11 1ar | ll111ar | Wrexham | Wrecsam | Abenbury WwTW | 3623 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333545 | 350419 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1AT | LL111AT | ll11 1at | ll111at | Wrexham | Wrecsam | Abenbury WwTW | 3675 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333469 | 350397 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1AU | LL111AU | ll11 1au | ll111au | Wrexham | Wrecsam | Abenbury WwTW | 3775 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333457 | 350560 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1AY | LL111AY | ll11 1ay | ll111ay | Wrexham | Wrecsam | Abenbury WwTW | 3722 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333471 | 350486 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1BA | LL111BA | ll11 1ba | ll111ba | Wrexham | Wrecsam | Abenbury WwTW | 3712 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333413 | 350378 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1BB | LL111BB | ll11 1bb | ll111bb | Wrexham | Wrecsam | Abenbury WwTW | 3659 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333449 | 350336 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1BD | LL111BD | ll11 1bd | ll111bd | Wrexham | Wrecsam | Abenbury WwTW | 3676 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333421 | 350323 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1BE | LL111BE | ll11 1be | ll111be | Wrexham | Wrecsam | Abenbury WwTW | 3562 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333517 | 350262 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1BG | LL111BG | ll11 1bg | ll111bg | Wrexham | Wrecsam | Abenbury WwTW | 3595 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333484 | 350272 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1BS | LL111BS | ll11 1bs | ll111bs | Wrexham | Wrecsam | Abenbury WwTW | 4010 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333222 | 350631 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1BT | LL111BT | ll11 1bt | ll111bt | Wrexham | Wrecsam | Abenbury WwTW | 4011 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333323 | 350778 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1BU | LL111BU | ll11 1bu | ll111bu | Wrexham | Wrecsam | Abenbury WwTW | 3965 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333266 | 350616 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1BW | LL111BW | ll11 1bw | ll111bw | Wrexham | Wrecsam | Abenbury WwTW | 4019 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333261 | 350705 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1BX | LL111BX | ll11 1bx | ll111bx | Wrexham | Wrecsam | Abenbury WwTW | 4048 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333171 | 350624 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1DE | LL111DE | ll11 1de | ll111de | Wrexham | Wrecsam | Abenbury WwTW | 4014 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333291 | 350739 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1DN | LL111DN | ll11 1dn | ll111dn | Wrexham | Wrecsam | Abenbury WwTW | 3961 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333235 | 350563 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1DP | LL111DP | ll11 1dp | ll111dp | Wrexham | Wrecsam | Abenbury WwTW | 3938 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333356 | 350698 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1DY | LL111DY | ll11 1dy | ll111dy | Wrexham | Wrecsam | Abenbury WwTW | 3948 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333509 | 350914 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1EB | LL111EB | ll11 1eb | ll111eb | Wrexham | Wrecsam | Abenbury WwTW | 3903 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333387 | 350681 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1EF | LL111EF | ll11 1ef | ll111ef | Wrexham | Wrecsam | Abenbury WwTW | 4175 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333098 | 350742 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1EH | LL111EH | ll11 1eh | ll111eh | Wrexham | Wrecsam | Abenbury WwTW | 4090 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333164 | 350688 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1EL | LL111EL | ll11 1el | ll111el | Wrexham | Wrecsam | Abenbury WwTW | 4180 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333142 | 350815 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1EP | LL111EP | ll11 1ep | ll111ep | Wrexham | Wrecsam | Abenbury WwTW | 4007 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333394 | 350864 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1EQ | LL111EQ | ll11 1eq | ll111eq | Wrexham | Wrecsam | Abenbury WwTW | 3829 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333397 | 350568 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1EW | LL111EW | ll11 1ew | ll111ew | Wrexham | Wrecsam | Abenbury WwTW | 4004 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333546 | 351044 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1HE | LL111HE | ll11 1he | ll111he | Wrexham | Wrecsam | Abenbury WwTW | 3906 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333241 | 350470 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1HF | LL111HF | ll11 1hf | ll111hf | Wrexham | Wrecsam | Abenbury WwTW | 3923 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333245 | 350508 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1HG | LL111HG | ll11 1hg | ll111hg | Wrexham | Wrecsam | Abenbury WwTW | 3917 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333274 | 350542 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1HH | LL111HH | ll11 1hh | ll111hh | Wrexham | Wrecsam | Abenbury WwTW | 3922 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333258 | 350527 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1HR | LL111HR | ll11 1hr | ll111hr | Wrexham | Wrecsam | Abenbury WwTW | 3898 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333361 | 350636 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1LA | LL111LA | ll11 1la | ll111la | Wrexham | Wrecsam | Abenbury WwTW | 3899 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333357 | 350632 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1LE | LL111LE | ll11 1le | ll111le | Wrexham | Wrecsam | Abenbury WwTW | 3905 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333245 | 350474 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1LF | LL111LF | ll11 1lf | ll111lf | Wrexham | Wrecsam | Abenbury WwTW | 3877 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333357 | 350593 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1LG | LL111LG | ll11 1lg | ll111lg | Wrexham | Wrecsam | Abenbury WwTW | 3873 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333290 | 350485 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1LH | LL111LH | ll11 1lh | ll111lh | Wrexham | Wrecsam | Abenbury WwTW | 3818 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333349 | 350476 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1LN | LL111LN | ll11 1ln | ll111ln | Wrexham | Wrecsam | Abenbury WwTW | 3863 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333289 | 350466 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1LP | LL111LP | ll11 1lp | ll111lp | Wrexham | Wrecsam | Abenbury WwTW | 3750 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333419 | 350458 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1LR | LL111LR | ll11 1lr | ll111lr | Wrexham | Wrecsam | Abenbury WwTW | 3774 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333380 | 350442 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1LS | LL111LS | ll11 1ls | ll111ls | Wrexham | Wrecsam | Abenbury WwTW | 3773 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333393 | 350461 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1LW | LL111LW | ll11 1lw | ll111lw | Wrexham | Wrecsam | Abenbury WwTW | 3799 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333343 | 350431 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1LY | LL111LY | ll11 1ly | ll111ly | Wrexham | Wrecsam | Abenbury WwTW | 3778 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333388 | 350463 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1NA | LL111NA | ll11 1na | ll111na | Wrexham | Wrecsam | Abenbury WwTW | 3832 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333376 | 350541 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1NB | LL111NB | ll11 1nb | ll111nb | Wrexham | Wrecsam | Abenbury WwTW | 3818 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333359 | 350490 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1ND | LL111ND | ll11 1nd | ll111nd | Wrexham | Wrecsam | Abenbury WwTW | 3822 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333371 | 350516 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1NE | LL111NE | ll11 1ne | ll111ne | Wrexham | Wrecsam | Abenbury WwTW | 3794 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333403 | 350513 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1NF | LL111NF | ll11 1nf | ll111nf | Wrexham | Wrecsam | Abenbury WwTW | 3819 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333433 | 350601 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1NH | LL111NH | ll11 1nh | ll111nh | Wrexham | Wrecsam | Abenbury WwTW | 3844 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333340 | 350510 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1NL | LL111NL | ll11 1nl | ll111nl | Wrexham | Wrecsam | Abenbury WwTW | 3845 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333332 | 350498 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1PA | LL111PA | ll11 1pa | ll111pa | Wrexham | Wrecsam | Abenbury WwTW | 4110 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333084 | 350603 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1PF | LL111PF | ll11 1pf | ll111pf | Wrexham | Wrecsam | Abenbury WwTW | 4159 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333023 | 350597 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1PP | LL111PP | ll11 1pp | ll111pp | Wrexham | Wrecsam | Abenbury WwTW | 4081 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333145 | 350644 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1PR | LL111PR | ll11 1pr | ll111pr | Wrexham | Wrecsam | Abenbury WwTW | 4054 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333126 | 350564 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1RB | LL111RB | ll11 1rb | ll111rb | Wrexham | Wrecsam | Abenbury WwTW | 3977 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333160 | 350474 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1RE | LL111RE | ll11 1re | ll111re | Wrexham | Wrecsam | Abenbury WwTW | 3948 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333208 | 350495 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1RN | LL111RN | ll11 1rn | ll111rn | Wrexham | Wrecsam | Abenbury WwTW | 3803 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333312 | 350388 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1RR | LL111RR | ll11 1rr | ll111rr | Wrexham | Wrecsam | Abenbury WwTW | 3894 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333248 | 350458 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1RY | LL111RY | ll11 1ry | ll111ry | Wrexham | Wrecsam | Abenbury WwTW | 3863 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333256 | 350412 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1SA | LL111SA | ll11 1sa | ll111sa | Wrexham | Wrecsam | Abenbury WwTW | 3775 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333350 | 350396 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1SD | LL111SD | ll11 1sd | ll111sd | Wrexham | Wrecsam | Abenbury WwTW | 3965 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333266 | 350616 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1SE | LL111SE | ll11 1se | ll111se | Wrexham | Wrecsam | Abenbury WwTW | 3792 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333335 | 350405 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1SG | LL111SG | ll11 1sg | ll111sg | Wrexham | Wrecsam | Abenbury WwTW | 3745 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333365 | 350364 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1SN | LL111SN | ll11 1sn | ll111sn | Wrexham | Wrecsam | Abenbury WwTW | 3755 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333326 | 350319 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1SP | LL111SP | ll11 1sp | ll111sp | Wrexham | Wrecsam | Abenbury WwTW | 3716 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333355 | 350291 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1SU | LL111SU | ll11 1su | ll111su | Wrexham | Wrecsam | Abenbury WwTW | 3719 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333361 | 350308 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1TA | LL111TA | ll11 1ta | ll111ta | Wrexham | Wrecsam | Abenbury WwTW | 3618 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333429 | 350223 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1WZ | LL111WZ | ll11 1wz | ll111wz | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 1ZA | LL111ZA | ll11 1za | ll111za | Wrexham | Wrecsam | Abenbury WwTW | 3722 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333471 | 350486 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AA | LL112AA | ll11 2aa | ll112aa | Wrexham | Wrecsam | Abenbury WwTW | 4302 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332989 | 350808 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AD | LL112AD | ll11 2ad | ll112ad | Wrexham | Wrecsam | Abenbury WwTW | 4418 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332851 | 350810 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AE | LL112AE | ll11 2ae | ll112ae | Wrexham | Wrecsam | Abenbury WwTW | 4524 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332778 | 350891 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AF | LL112AF | ll11 2af | ll112af | Wrexham | Wrecsam | Abenbury WwTW | 4708 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332623 | 350991 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AG | LL112AG | ll11 2ag | ll112ag | Wrexham | Wrecsam | Abenbury WwTW | 4913 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 332473 | 351136 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AH | LL112AH | ll11 2ah | ll112ah | Wrexham | Wrecsam | Abenbury WwTW | 4554 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332779 | 350947 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AJ | LL112AJ | ll11 2aj | ll112aj | Wrexham | Wrecsam | Abenbury WwTW | 4561 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332673 | 350795 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AP | LL112AP | ll11 2ap | ll112ap | Wrexham | Wrecsam | Abenbury WwTW | 4420 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332798 | 350730 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AQ | LL112AQ | ll11 2aq | ll112aq | Wrexham | Wrecsam | Abenbury WwTW | 4517 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332691 | 350741 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AR | LL112AR | ll11 2ar | ll112ar | Wrexham | Wrecsam | Abenbury WwTW | 4456 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332804 | 350807 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AS | LL112AS | ll11 2as | ll112as | Wrexham | Wrecsam | Gresford STW | 3070 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333580 | 353000 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AT | LL112AT | ll11 2at | ll112at | Wrexham | Wrecsam | Abenbury WwTW | 4536 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332734 | 350847 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AU | LL112AU | ll11 2au | ll112au | Wrexham | Wrecsam | Gresford STW | 3023 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333592 | 353046 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AW | LL112AW | ll11 2aw | ll112aw | Wrexham | Wrecsam | Abenbury WwTW | 4723 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332658 | 351070 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AX | LL112AX | ll11 2ax | ll112ax | Wrexham | Wrecsam | Abenbury WwTW | 4748 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332555 | 350960 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AY | LL112AY | ll11 2ay | ll112ay | Wrexham | Wrecsam | Abenbury WwTW | 4502 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332679 | 350692 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2AZ | LL112AZ | ll11 2az | ll112az | Wrexham | Wrecsam | Abenbury WwTW | 4729 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332534 | 350890 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BA | LL112BA | ll11 2ba | ll112ba | Wrexham | Wrecsam | Gresford STW | 4887 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332617 | 351450 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BB | LL112BB | ll11 2bb | ll112bb | Wrexham | Wrecsam | Abenbury WwTW | 4610 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332661 | 350869 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BD | LL112BD | ll11 2bd | ll112bd | Wrexham | Wrecsam | Abenbury WwTW | 4853 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 332473 | 351027 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BE | LL112BE | ll11 2be | ll112be | Wrexham | Wrecsam | Abenbury WwTW | 4939 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 332403 | 351077 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BF | LL112BF | ll11 2bf | ll112bf | Wrexham | Wrecsam | Gresford STW | 4377 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332725 | 351972 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BG | LL112BG | ll11 2bg | ll112bg | Wrexham | Wrecsam | Abenbury WwTW | 4921 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 332358 | 350970 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BH | LL112BH | ll11 2bh | ll112bh | Wrexham | Wrecsam | Abenbury WwTW | 4972 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 332375 | 351093 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BJ | LL112BJ | ll11 2bj | ll112bj | Wrexham | Wrecsam | Gresford STW | 4362 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332801 | 351947 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BL | LL112BL | ll11 2bl | ll112bl | Wrexham | Wrecsam | Abenbury WwTW | 5049 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 332290 | 351103 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BP | LL112BP | ll11 2bp | ll112bp | Wrexham | Wrecsam | Gresford STW | 4710 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332808 | 351552 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BQ | LL112BQ | ll11 2bq | ll112bq | Wrexham | Wrecsam | Gresford STW | 4479 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332773 | 351829 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BS | LL112BS | ll11 2bs | ll112bs | Wrexham | Wrecsam | Gresford STW | 4627 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332833 | 351632 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BT | LL112BT | ll11 2bt | ll112bt | Wrexham | Wrecsam | Gresford STW | 4564 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332871 | 351684 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BU | LL112BU | ll11 2bu | ll112bu | Wrexham | Wrecsam | Gresford STW | 4611 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332737 | 351699 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BW | LL112BW | ll11 2bw | ll112bw | Wrexham | Wrecsam | Gresford STW | 4732 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332747 | 351558 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BX | LL112BX | ll11 2bx | ll112bx | Wrexham | Wrecsam | Gresford STW | 4327 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332767 | 352006 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BY | LL112BY | ll11 2by | ll112by | Wrexham | Wrecsam | Abenbury WwTW | 4330 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332880 | 350691 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2BZ | LL112BZ | ll11 2bz | ll112bz | Wrexham | Wrecsam | Abenbury WwTW | 4837 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332713 | 351340 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2DB | LL112DB | ll11 2db | ll112db | Wrexham | Wrecsam | Abenbury WwTW | 4332 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332840 | 350630 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2DD | LL112DD | ll11 2dd | ll112dd | Wrexham | Wrecsam | Gresford STW | 4532 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332927 | 351692 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2DE | LL112DE | ll11 2de | ll112de | Wrexham | Wrecsam | Gresford STW | 4461 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332850 | 351809 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2DF | LL112DF | ll11 2df | ll112df | Wrexham | Wrecsam | Gresford STW | 4435 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332896 | 351815 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2DG | LL112DG | ll11 2dg | ll112dg | Wrexham | Wrecsam | Gresford STW | 4455 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332929 | 351777 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2DH | LL112DH | ll11 2dh | ll112dh | Wrexham | Wrecsam | Gresford STW | 4498 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332955 | 351717 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2DJ | LL112DJ | ll11 2dj | ll112dj | Wrexham | Wrecsam | Abenbury WwTW | 4822 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332756 | 351371 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2DL | LL112DL | ll11 2dl | ll112dl | Wrexham | Wrecsam | Gresford STW | 4480 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332958 | 351735 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2DP | LL112DP | ll11 2dp | ll112dp | Wrexham | Wrecsam | Gresford STW | 4433 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332702 | 351921 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2DQ | LL112DQ | ll11 2dq | ll112dq | Wrexham | Wrecsam | Abenbury WwTW | 4754 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332790 | 351304 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2EA | LL112EA | ll11 2ea | ll112ea | Wrexham | Wrecsam | Abenbury WwTW | 4573 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333111 | 351411 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2ED | LL112ED | ll11 2ed | ll112ed | Wrexham | Wrecsam | Gresford STW | 4578 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333120 | 351556 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2EE | LL112EE | ll11 2ee | ll112ee | Wrexham | Wrecsam | Gresford STW | 4583 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333167 | 351531 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2EF | LL112EF | ll11 2ef | ll112ef | Wrexham | Wrecsam | Gresford STW | 4504 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333213 | 351597 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2EG | LL112EG | ll11 2eg | ll112eg | Wrexham | Wrecsam | Gresford STW | 4478 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333289 | 351596 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2EH | LL112EH | ll11 2eh | ll112eh | Wrexham | Wrecsam | Gresford STW | 4359 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333428 | 351672 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2EN | LL112EN | ll11 2en | ll112en | Wrexham | Wrecsam | Gresford STW | 4430 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333442 | 351592 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2EP | LL112EP | ll11 2ep | ll112ep | Wrexham | Wrecsam | Abenbury WwTW | 4539 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333216 | 351476 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2ER | LL112ER | ll11 2er | ll112er | Wrexham | Wrecsam | Abenbury WwTW | 4562 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333156 | 351445 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2ES | LL112ES | ll11 2es | ll112es | Wrexham | Wrecsam | Gresford STW | 4598 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333067 | 351556 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2ET | LL112ET | ll11 2et | ll112et | Wrexham | Wrecsam | Gresford STW | 4403 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333155 | 351731 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2EU | LL112EU | ll11 2eu | ll112eu | Wrexham | Wrecsam | Gresford STW | 4390 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333065 | 351784 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2EW | LL112EW | ll11 2ew | ll112ew | Wrexham | Wrecsam | Abenbury WwTW | 4408 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333461 | 351542 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2EY | LL112EY | ll11 2ey | ll112ey | Wrexham | Wrecsam | Gresford STW | 4444 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333142 | 351692 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2EZ | LL112EZ | ll11 2ez | ll112ez | Wrexham | Wrecsam | Gresford STW | 3888 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332971 | 352394 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HA | LL112HA | ll11 2ha | ll112ha | Wrexham | Wrecsam | Gresford STW | 4328 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333180 | 351801 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HB | LL112HB | ll11 2hb | ll112hb | Wrexham | Wrecsam | Gresford STW | 4465 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333147 | 351667 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HD | LL112HD | ll11 2hd | ll112hd | Wrexham | Wrecsam | Gresford STW | 4231 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333023 | 351980 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HE | LL112HE | ll11 2he | ll112he | Wrexham | Wrecsam | Gresford STW | 4328 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333026 | 351871 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HF | LL112HF | ll11 2hf | ll112hf | Wrexham | Wrecsam | Gresford STW | 4245 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332947 | 352002 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HG | LL112HG | ll11 2hg | ll112hg | Wrexham | Wrecsam | Gresford STW | 4296 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333008 | 351915 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HH | LL112HH | ll11 2hh | ll112hh | Wrexham | Wrecsam | Gresford STW | 4088 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333063 | 352120 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HJ | LL112HJ | ll11 2hj | ll112hj | Wrexham | Wrecsam | Gresford STW | 4175 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333051 | 352028 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HL | LL112HL | ll11 2hl | ll112hl | Wrexham | Wrecsam | Gresford STW | 3996 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333105 | 352201 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HN | LL112HN | ll11 2hn | ll112hn | Wrexham | Wrecsam | Gresford STW | 3955 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333111 | 352244 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HQ | LL112HQ | ll11 2hq | ll112hq | Wrexham | Wrecsam | Gresford STW | 4052 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333145 | 352120 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HR | LL112HR | ll11 2hr | ll112hr | Wrexham | Wrecsam | Gresford STW | 4643 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332917 | 351574 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HS | LL112HS | ll11 2hs | ll112hs | Wrexham | Wrecsam | Abenbury WwTW | 4643 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332997 | 351385 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HT | LL112HT | ll11 2ht | ll112ht | Wrexham | Wrecsam | Abenbury WwTW | 4528 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332881 | 351049 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HU | LL112HU | ll11 2hu | ll112hu | Wrexham | Wrecsam | Abenbury WwTW | 4645 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332961 | 351345 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HW | LL112HW | ll11 2hw | ll112hw | Wrexham | Wrecsam | Gresford STW | 3919 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333114 | 352283 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HX | LL112HX | ll11 2hx | ll112hx | Wrexham | Wrecsam | Gresford STW | 4077 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333145 | 352092 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HY | LL112HY | ll11 2hy | ll112hy | Wrexham | Wrecsam | Abenbury WwTW | 4617 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332972 | 351314 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2HZ | LL112HZ | ll11 2hz | ll112hz | Wrexham | Wrecsam | Gresford STW | 4236 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333097 | 351939 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2JA | LL112JA | ll11 2ja | ll112ja | Wrexham | Wrecsam | Abenbury WwTW | 4362 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333181 | 351167 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2JB | LL112JB | ll11 2jb | ll112jb | Wrexham | Wrecsam | Abenbury WwTW | 4462 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332938 | 351015 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2JD | LL112JD | ll11 2jd | ll112jd | Wrexham | Wrecsam | Gresford STW | 4560 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332965 | 351643 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2JE | LL112JE | ll11 2je | ll112je | Wrexham | Wrecsam | Gresford STW | 4646 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332974 | 351545 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LA | LL112LA | ll11 2la | ll112la | Wrexham | Wrecsam | Gresford STW | 4167 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332958 | 352084 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LB | LL112LB | ll11 2lb | ll112lb | Wrexham | Wrecsam | Gresford STW | 3970 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333036 | 352266 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LD | LL112LD | ll11 2ld | ll112ld | Wrexham | Wrecsam | Gresford STW | 4025 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332994 | 352226 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LE | LL112LE | ll11 2le | ll112le | Wrexham | Wrecsam | Gresford STW | 4109 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333002 | 352127 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LF | LL112LF | ll11 2lf | ll112lf | Wrexham | Wrecsam | Gresford STW | 4030 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333017 | 352208 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LG | LL112LG | ll11 2lg | ll112lg | Wrexham | Wrecsam | Gresford STW | 4084 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332958 | 352178 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LH | LL112LH | ll11 2lh | ll112lh | Wrexham | Wrecsam | Gresford STW | 3988 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333070 | 352228 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LL | LL112LL | ll11 2ll | ll112ll | Wrexham | Wrecsam | Gresford STW | 3944 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333056 | 352285 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LN | LL112LN | ll11 2ln | ll112ln | Wrexham | Wrecsam | Abenbury WwTW | 4100 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333243 | 350819 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LP | LL112LP | ll11 2lp | ll112lp | Wrexham | Wrecsam | Abenbury WwTW | 4053 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333363 | 350900 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LR | LL112LR | ll11 2lr | ll112lr | Wrexham | Wrecsam | Abenbury WwTW | 4064 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333407 | 350972 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LS | LL112LS | ll11 2ls | ll112ls | Wrexham | Wrecsam | Abenbury WwTW | 4093 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333432 | 351047 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LT | LL112LT | ll11 2lt | ll112lt | Wrexham | Wrecsam | Abenbury WwTW | 4071 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333516 | 351111 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LU | LL112LU | ll11 2lu | ll112lu | Wrexham | Wrecsam | Abenbury WwTW | 4198 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333370 | 351136 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LW | LL112LW | ll11 2lw | ll112lw | Wrexham | Wrecsam | Abenbury WwTW | 4074 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333258 | 350795 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2LY | LL112LY | ll11 2ly | ll112ly | Wrexham | Wrecsam | Abenbury WwTW | 4156 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333371 | 351073 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NA | LL112NA | ll11 2na | ll112na | Wrexham | Wrecsam | Abenbury WwTW | 4161 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333495 | 351221 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NB | LL112NB | ll11 2nb | ll112nb | Wrexham | Wrecsam | Abenbury WwTW | 4361 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333341 | 351350 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2ND | LL112ND | ll11 2nd | ll112nd | Wrexham | Wrecsam | Abenbury WwTW | 4377 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333304 | 351332 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NE | LL112NE | ll11 2ne | ll112ne | Wrexham | Wrecsam | Abenbury WwTW | 4446 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333202 | 351322 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NF | LL112NF | ll11 2nf | ll112nf | Wrexham | Wrecsam | Abenbury WwTW | 4501 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333142 | 351336 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NG | LL112NG | ll11 2ng | ll112ng | Wrexham | Wrecsam | Abenbury WwTW | 4436 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333175 | 351275 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NH | LL112NH | ll11 2nh | ll112nh | Wrexham | Wrecsam | Abenbury WwTW | 4417 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333203 | 351279 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NJ | LL112NJ | ll11 2nj | ll112nj | Wrexham | Wrecsam | Abenbury WwTW | 4249 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333448 | 351301 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NL | LL112NL | ll11 2nl | ll112nl | Wrexham | Wrecsam | Abenbury WwTW | 4420 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333141 | 351209 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NN | LL112NN | ll11 2nn | ll112nn | Wrexham | Wrecsam | Abenbury WwTW | 4368 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333271 | 351282 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NP | LL112NP | ll11 2np | ll112np | Wrexham | Wrecsam | Abenbury WwTW | 4292 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333272 | 351166 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NQ | LL112NQ | ll11 2nq | ll112nq | Wrexham | Wrecsam | Abenbury WwTW | 4319 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333362 | 351310 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NR | LL112NR | ll11 2nr | ll112nr | Wrexham | Wrecsam | Abenbury WwTW | 4278 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333338 | 351222 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NS | LL112NS | ll11 2ns | ll112ns | Wrexham | Wrecsam | Abenbury WwTW | 4145 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333324 | 350998 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NT | LL112NT | ll11 2nt | ll112nt | Wrexham | Wrecsam | Abenbury WwTW | 4195 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333310 | 351060 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NU | LL112NU | ll11 2nu | ll112nu | Wrexham | Wrecsam | Abenbury WwTW | 4208 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333198 | 350940 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NW | LL112NW | ll11 2nw | ll112nw | Wrexham | Wrecsam | Abenbury WwTW | 4306 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333233 | 351142 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NX | LL112NX | ll11 2nx | ll112nx | Wrexham | Wrecsam | Abenbury WwTW | 4312 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333115 | 351001 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NY | LL112NY | ll11 2ny | ll112ny | Wrexham | Wrecsam | Abenbury WwTW | 4319 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333046 | 350920 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2NZ | LL112NZ | ll11 2nz | ll112nz | Wrexham | Wrecsam | Abenbury WwTW | 4225 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333422 | 351236 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PA | LL112PA | ll11 2pa | ll112pa | Wrexham | Wrecsam | Abenbury WwTW | 4210 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333234 | 350990 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PB | LL112PB | ll11 2pb | ll112pb | Wrexham | Wrecsam | Abenbury WwTW | 3991 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333602 | 351087 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PD | LL112PD | ll11 2pd | ll112pd | Wrexham | Wrecsam | Abenbury WwTW | 4536 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333084 | 351322 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PH | LL112PH | ll11 2ph | ll112ph | Wrexham | Wrecsam | Abenbury WwTW | 4355 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333579 | 351581 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PL | LL112PL | ll11 2pl | ll112pl | Wrexham | Wrecsam | Gresford STW | 4367 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333547 | 351623 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PN | LL112PN | ll11 2pn | ll112pn | Wrexham | Wrecsam | Gresford STW | 4160 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333583 | 351829 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PP | LL112PP | ll11 2pp | ll112pp | Wrexham | Wrecsam | Gresford STW | 4284 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333617 | 351688 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PR | LL112PR | ll11 2pr | ll112pr | Wrexham | Wrecsam | Gresford STW | 4294 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333521 | 351708 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PS | LL112PS | ll11 2ps | ll112ps | Wrexham | Wrecsam | Gresford STW | 4257 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333511 | 351751 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PT | LL112PT | ll11 2pt | ll112pt | Wrexham | Wrecsam | Gresford STW | 4161 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333483 | 351862 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PU | LL112PU | ll11 2pu | ll112pu | Wrexham | Wrecsam | Gresford STW | 3998 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333533 | 352017 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PW | LL112PW | ll11 2pw | ll112pw | Wrexham | Wrecsam | Gresford STW | 4112 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333558 | 351888 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PX | LL112PX | ll11 2px | ll112px | Wrexham | Wrecsam | Gresford STW | 3861 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333687 | 352109 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2PY | LL112PY | ll11 2py | ll112py | Wrexham | Wrecsam | Gresford STW | 3951 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333659 | 352024 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RA | LL112RA | ll11 2ra | ll112ra | Wrexham | Wrecsam | Gresford STW | 3999 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333451 | 352047 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RB | LL112RB | ll11 2rb | ll112rb | Wrexham | Wrecsam | Gresford STW | 4259 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333403 | 351787 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RD | LL112RD | ll11 2rd | ll112rd | Wrexham | Wrecsam | Gresford STW | 4230 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333327 | 351847 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RE | LL112RE | ll11 2re | ll112re | Wrexham | Wrecsam | Gresford STW | 4087 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333403 | 351971 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RF | LL112RF | ll11 2rf | ll112rf | Wrexham | Wrecsam | Gresford STW | 4131 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333365 | 351938 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RG | LL112RG | ll11 2rg | ll112rg | Wrexham | Wrecsam | Gresford STW | 4148 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333319 | 351939 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RH | LL112RH | ll11 2rh | ll112rh | Wrexham | Wrecsam | Gresford STW | 4132 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333243 | 351988 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RL | LL112RL | ll11 2rl | ll112rl | Wrexham | Wrecsam | Gresford STW | 4282 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333219 | 351835 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RN | LL112RN | ll11 2rn | ll112rn | Wrexham | Wrecsam | Gresford STW | 4246 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333249 | 351861 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RP | LL112RP | ll11 2rp | ll112rp | Wrexham | Wrecsam | Gresford STW | 4450 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333266 | 351635 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RR | LL112RR | ll11 2rr | ll112rr | Wrexham | Wrecsam | Gresford STW | 4339 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333355 | 351719 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RS | LL112RS | ll11 2rs | ll112rs | Wrexham | Wrecsam | Gresford STW | 3908 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333497 | 352126 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2RW | LL112RW | ll11 2rw | ll112rw | Wrexham | Wrecsam | Gresford STW | 4379 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333296 | 351699 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SA | LL112SA | ll11 2sa | ll112sa | Wrexham | Wrecsam | Abenbury WwTW | 3854 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333644 | 350928 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SD | LL112SD | ll11 2sd | ll112sd | Wrexham | Wrecsam | Abenbury WwTW | 3980 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333648 | 351120 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SE | LL112SE | ll11 2se | ll112se | Wrexham | Wrecsam | Abenbury WwTW | 4026 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333604 | 351141 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SF | LL112SF | ll11 2sf | ll112sf | Wrexham | Wrecsam | Abenbury WwTW | 4118 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333607 | 351277 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SG | LL112SG | ll11 2sg | ll112sg | Wrexham | Wrecsam | Abenbury WwTW | 4330 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333618 | 351584 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SH | LL112SH | ll11 2sh | ll112sh | Wrexham | Wrecsam | Gresford STW | 4077 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333702 | 351878 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SJ | LL112SJ | ll11 2sj | ll112sj | Wrexham | Wrecsam | Abenbury WwTW | 3897 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333576 | 350915 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SL | LL112SL | ll11 2sl | ll112sl | Wrexham | Wrecsam | Gresford STW | 4106 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333760 | 351831 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SN | LL112SN | ll11 2sn | ll112sn | Wrexham | Wrecsam | Gresford STW | 3872 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333778 | 352070 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SP | LL112SP | ll11 2sp | ll112sp | Wrexham | Wrecsam | Gresford STW | 3786 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333674 | 352193 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SQ | LL112SQ | ll11 2sq | ll112sq | Wrexham | Wrecsam | Gresford STW | 3824 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333840 | 352102 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SR | LL112SR | ll11 2sr | ll112sr | Wrexham | Wrecsam | Gresford STW | 3832 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333674 | 352144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SS | LL112SS | ll11 2ss | ll112ss | Wrexham | Wrecsam | Gresford STW | 3882 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333571 | 352127 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2ST | LL112ST | ll11 2st | ll112st | Wrexham | Wrecsam | Gresford STW | 3794 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333530 | 352236 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SU | LL112SU | ll11 2su | ll112su | Wrexham | Wrecsam | Gresford STW | 3691 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333587 | 352324 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SW | LL112SW | ll11 2sw | ll112sw | Wrexham | Wrecsam | Gresford STW | 3841 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333735 | 352115 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2SY | LL112SY | ll11 2sy | ll112sy | Wrexham | Wrecsam | Gresford STW | 3587 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333548 | 352451 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TA | LL112TA | ll11 2ta | ll112ta | Wrexham | Wrecsam | Gresford STW | 3558 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333575 | 352471 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TB | LL112TB | ll11 2tb | ll112tb | Wrexham | Wrecsam | Gresford STW | 3552 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333476 | 352519 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TD | LL112TD | ll11 2td | ll112td | Wrexham | Wrecsam | Gresford STW | 3714 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333480 | 352341 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TE | LL112TE | ll11 2te | ll112te | Wrexham | Wrecsam | Gresford STW | 3817 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333449 | 352243 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TF | LL112TF | ll11 2tf | ll112tf | Wrexham | Wrecsam | Gresford STW | 3729 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333502 | 352316 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TG | LL112TG | ll11 2tg | ll112tg | Wrexham | Wrecsam | Gresford STW | 3657 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333394 | 352440 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TH | LL112TH | ll11 2th | ll112th | Wrexham | Wrecsam | Gresford STW | 3664 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333356 | 352449 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TJ | LL112TJ | ll11 2tj | ll112tj | Wrexham | Wrecsam | Gresford STW | 3971 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333318 | 352131 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TL | LL112TL | ll11 2tl | ll112tl | Wrexham | Wrecsam | Gresford STW | 3655 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333454 | 352416 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TN | LL112TN | ll11 2tn | ll112tn | Wrexham | Wrecsam | Gresford STW | 3800 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333348 | 352304 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TP | LL112TP | ll11 2tp | ll112tp | Wrexham | Wrecsam | Gresford STW | 3804 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333613 | 352195 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TR | LL112TR | ll11 2tr | ll112tr | Wrexham | Wrecsam | Gresford STW | 3739 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333223 | 352430 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TS | LL112TS | ll11 2ts | ll112ts | Wrexham | Wrecsam | Gresford STW | 3676 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333269 | 352477 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2TT | LL112TT | ll11 2tt | ll112tt | Wrexham | Wrecsam | Gresford STW | 3779 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 333174 | 352409 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UA | LL112UA | ll11 2ua | ll112ua | Wrexham | Wrecsam | Gresford STW | 3081 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333673 | 352946 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UB | LL112UB | ll11 2ub | ll112ub | Wrexham | Wrecsam | Gresford STW | 3057 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333234 | 353205 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UD | LL112UD | ll11 2ud | ll112ud | Wrexham | Wrecsam | Gresford STW | 3044 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333288 | 353187 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UE | LL112UE | ll11 2ue | ll112ue | Wrexham | Wrecsam | Gresford STW | 3058 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333362 | 353127 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UF | LL112UF | ll11 2uf | ll112uf | Wrexham | Wrecsam | Gresford STW | 3088 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333431 | 353054 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UG | LL112UG | ll11 2ug | ll112ug | Wrexham | Wrecsam | Gresford STW | 3022 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333497 | 353094 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UH | LL112UH | ll11 2uh | ll112uh | Wrexham | Wrecsam | Gresford STW | 2934 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333537 | 353173 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UL | LL112UL | ll11 2ul | ll112ul | Wrexham | Wrecsam | Gresford STW | 3596 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333318 | 352542 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UP | LL112UP | ll11 2up | ll112up | Wrexham | Wrecsam | Gresford STW | 3292 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333621 | 352740 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UQ | LL112UQ | ll11 2uq | ll112uq | Wrexham | Wrecsam | Gresford STW | 3081 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333381 | 353090 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UR | LL112UR | ll11 2ur | ll112ur | Wrexham | Wrecsam | Gresford STW | 3331 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333690 | 352670 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2US | LL112US | ll11 2us | ll112us | Wrexham | Wrecsam | Gresford STW | 3212 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333612 | 352830 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UT | LL112UT | ll11 2ut | ll112ut | Wrexham | Wrecsam | Gresford STW | 3346 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333495 | 352735 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UU | LL112UU | ll11 2uu | ll112uu | Wrexham | Wrecsam | Gresford STW | 3484 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333410 | 352623 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UW | LL112UW | ll11 2uw | ll112uw | Wrexham | Wrecsam | Gresford STW | 3256 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333664 | 352761 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2UY | LL112UY | ll11 2uy | ll112uy | Wrexham | Wrecsam | Gresford STW | 3466 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333535 | 352587 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2YA | LL112YA | ll11 2ya | ll112ya | Wrexham | Wrecsam | Gresford STW | 3414 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333729 | 352567 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2YB | LL112YB | ll11 2yb | ll112yb | Wrexham | Wrecsam | Gresford STW | 3641 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333701 | 352337 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2YD | LL112YD | ll11 2yd | ll112yd | Wrexham | Wrecsam | Gresford STW | 3524 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333625 | 352488 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2YE | LL112YE | ll11 2ye | ll112ye | Wrexham | Wrecsam | Gresford STW | 3522 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333675 | 352472 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2YF | LL112YF | ll11 2yf | ll112yf | Wrexham | Wrecsam | Gresford STW | 3456 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333645 | 352554 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2YG | LL112YG | ll11 2yg | ll112yg | Wrexham | Wrecsam | Gresford STW | 3437 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333556 | 352610 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 2YH | LL112YH | ll11 2yh | ll112yh | Wrexham | Wrecsam | Gresford STW | 2983 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333637 | 353069 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3AA | LL113AA | ll11 3aa | ll113aa | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 2468 | 1072 | 900to1200 | 2.15 | 1.57 | 1.15 | 19.98 | 10.66 | 11.78 | 321998 | 351948 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AB | LL113AB | ll11 3ab | ll113ab | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 957 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 320488 | 351889 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AD | LL113AD | ll11 3ad | ll113ad | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 265 | 1015 | 900to1200 | 2.03 | 1.49 | 1.09 | 18.92 | 10.09 | 11.15 | 319271 | 351788 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AE | LL113AE | ll11 3ae | ll113ae | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 1337 | 1027 | 900to1200 | 2.06 | 1.5 | 1.1 | 19.14 | 10.21 | 11.28 | 320833 | 352127 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AF | LL113AF | ll11 3af | ll113af | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 228 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 319642 | 351608 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AG | LL113AG | ll11 3ag | ll113ag | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 353 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 319869 | 351924 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AH | LL113AH | ll11 3ah | ll113ah | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 1321 | 1010 | 900to1200 | 2.02 | 1.48 | 1.08 | 18.82 | 10.04 | 11.1 | 320452 | 352759 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AJ | LL113AJ | ll11 3aj | ll113aj | Wrexham | Wrecsam | Llanfynydd STW | 3929 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 327847 | 352829 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3AL | LL113AL | ll11 3al | ll113al | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 2039 | 980 | 900to1200 | 1.96 | 1.44 | 1.05 | 18.27 | 9.74 | 10.77 | 320432 | 353639 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AN | LL113AN | ll11 3an | ll113an | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 480 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 320012 | 351864 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AP | LL113AP | ll11 3ap | ll113ap | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 513 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 319726 | 352285 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AQ | LL113AQ | ll11 3aq | ll113aq | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 423 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 319694 | 352201 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AR | LL113AR | ll11 3ar | ll113ar | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 533 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 319662 | 352326 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AS | LL113AS | ll11 3as | ll113as | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 582 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 319586 | 352389 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AT | LL113AT | ll11 3at | ll113at | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 2149 | 976 | 900to1200 | 1.95 | 1.43 | 1.05 | 18.19 | 9.7 | 10.72 | 317895 | 353197 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AU | LL113AU | ll11 3au | ll113au | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 1420 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 318273 | 352460 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AW | LL113AW | ll11 3aw | ll113aw | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 479 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 319700 | 352259 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AX | LL113AX | ll11 3ax | ll113ax | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 376 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 319756 | 352113 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3AZ | LL113AZ | ll11 3az | ll113az | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 392 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 319825 | 352072 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3BA | LL113BA | ll11 3ba | ll113ba | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 1118 | 992 | 900to1200 | 1.99 | 1.45 | 1.07 | 18.49 | 9.86 | 10.9 | 318590 | 351213 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3BD | LL113BD | ll11 3bd | ll113bd | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 2611 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 318050 | 349662 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3BE | LL113BE | ll11 3be | ll113be | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 2599 | 1021 | 900to1200 | 2.04 | 1.5 | 1.1 | 19.03 | 10.15 | 11.22 | 319043 | 349258 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3BG | LL113BG | ll11 3bg | ll113bg | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 1307 | 1017 | 900to1200 | 2.04 | 1.49 | 1.09 | 18.96 | 10.11 | 11.17 | 320425 | 350853 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3BH | LL113BH | ll11 3bh | ll113bh | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 3104 | 1021 | 900to1200 | 2.04 | 1.5 | 1.1 | 19.03 | 10.15 | 11.22 | 319132 | 348732 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3BJ | LL113BJ | ll11 3bj | ll113bj | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 652 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 319689 | 352442 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3BN | LL113BN | ll11 3bn | ll113bn | Wrexham | Wrecsam | Abenbury WwTW | 5047 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 331846 | 350217 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3BP | LL113BP | ll11 3bp | ll113bp | Wrexham | Wrecsam | Llanfynydd STW | 6640 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 330247 | 350654 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3BQ | LL113BQ | ll11 3bq | ll113bq | Wrexham | Wrecsam | Abenbury WwTW | 5141 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 331753 | 350237 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3BS | LL113BS | ll11 3bs | ll113bs | Wrexham | Wrecsam | Abenbury WwTW | 6627 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 330344 | 350710 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3BT | LL113BT | ll11 3bt | ll113bt | Wrexham | Wrecsam | Llanfynydd STW | 6553 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 329137 | 350377 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3BU | LL113BU | ll11 3bu | ll113bu | Wrexham | Wrecsam | Llanfynydd STW | 4870 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328466 | 351956 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3BW | LL113BW | ll11 3bw | ll113bw | Wrexham | Wrecsam | Abenbury WwTW | 5595 | 853 | 700to900 | 1.71 | 1.25 | 0.92 | 15.9 | 8.48 | 9.37 | 331219 | 350082 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3BX | LL113BX | ll11 3bx | ll113bx | Wrexham | Wrecsam | Abenbury WwTW | 5175 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 331689 | 350162 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3BY | LL113BY | ll11 3by | ll113by | Wrexham | Wrecsam | Llanfynydd STW | 4789 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328005 | 351978 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3BZ | LL113BZ | ll11 3bz | ll113bz | Wrexham | Wrecsam | Abenbury WwTW | 5080 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 331817 | 350232 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DA | LL113DA | ll11 3da | ll113da | Wrexham | Wrecsam | Llanfynydd STW | 4938 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 326938 | 351861 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DB | LL113DB | ll11 3db | ll113db | Wrexham | Wrecsam | Llanfynydd STW | 4727 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 326579 | 352141 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DD | LL113DD | ll11 3dd | ll113dd | Wrexham | Wrecsam | Llanfynydd STW | 4913 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 326539 | 351959 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DE | LL113DE | ll11 3de | ll113de | Wrexham | Wrecsam | Llanfynydd STW | 4983 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 326105 | 352005 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DH | LL113DH | ll11 3dh | ll113dh | Wrexham | Wrecsam | Abenbury WwTW | 4813 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332061 | 350123 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DL | LL113DL | ll11 3dl | ll113dl | Wrexham | Wrecsam | Abenbury WwTW | 5036 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 331824 | 350127 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DN | LL113DN | ll11 3dn | ll113dn | Wrexham | Wrecsam | Abenbury WwTW | 4900 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 331987 | 350174 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DP | LL113DP | ll11 3dp | ll113dp | Wrexham | Wrecsam | Llanfynydd STW | 5248 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 326919 | 351551 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DQ | LL113DQ | ll11 3dq | ll113dq | Wrexham | Wrecsam | Llanfynydd STW | 5403 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329247 | 351600 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DR | LL113DR | ll11 3dr | ll113dr | Wrexham | Wrecsam | Llanfynydd STW | 5504 | 1097 | 900to1200 | 2.2 | 1.61 | 1.18 | 20.45 | 10.9 | 12.05 | 326497 | 351364 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DS | LL113DS | ll11 3ds | ll113ds | Wrexham | Wrecsam | Llanfynydd STW | 5574 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 327220 | 351192 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DT | LL113DT | ll11 3dt | ll113dt | Wrexham | Wrecsam | Llanfynydd STW | 5899 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 327335 | 350860 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DU | LL113DU | ll11 3du | ll113du | Wrexham | Wrecsam | Llanfynydd STW | 5738 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327622 | 351014 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DW | LL113DW | ll11 3dw | ll113dw | Wrexham | Wrecsam | Llanfynydd STW | 5068 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 326789 | 351752 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DX | LL113DX | ll11 3dx | ll113dx | Wrexham | Wrecsam | Abenbury WwTW | 4862 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332009 | 350125 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DY | LL113DY | ll11 3dy | ll113dy | Wrexham | Wrecsam | Llanfynydd STW | 5964 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327786 | 350790 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3DZ | LL113DZ | ll11 3dz | ll113dz | Wrexham | Wrecsam | Llanfynydd STW | 5807 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328786 | 351063 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EA | LL113EA | ll11 3ea | ll113ea | Wrexham | Wrecsam | Llanfynydd STW | 6491 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 327650 | 350261 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EB | LL113EB | ll11 3eb | ll113eb | Wrexham | Wrecsam | Llanfynydd STW | 5870 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 327313 | 350890 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3ED | LL113ED | ll11 3ed | ll113ed | Wrexham | Wrecsam | Llanfynydd STW | 5842 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 327288 | 350919 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EE | LL113EE | ll11 3ee | ll113ee | Wrexham | Wrecsam | Llanfynydd STW | 5986 | 1056 | 900to1200 | 2.11 | 1.55 | 1.13 | 19.68 | 10.5 | 11.6 | 327462 | 350768 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EF | LL113EF | ll11 3ef | ll113ef | Wrexham | Wrecsam | Abenbury WwTW | 4712 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332172 | 350131 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EG | LL113EG | ll11 3eg | ll113eg | Wrexham | Wrecsam | Llanfynydd STW | 5951 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329209 | 351017 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EH | LL113EH | ll11 3eh | ll113eh | Wrexham | Wrecsam | Llanfynydd STW | 5908 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329177 | 351053 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EJ | LL113EJ | ll11 3ej | ll113ej | Denbighshire | Sir Ddinbych | Pen-Y-Stryt WwTW | 455 | 1011 | 900to1200 | 2.02 | 1.48 | 1.09 | 18.84 | 10.05 | 11.11 | 319899 | 352081 | Denbighshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir Ddinbych | Denbighshire County Council
LL11 3EL | LL113EL | ll11 3el | ll113el | Wrexham | Wrecsam | Llanfynydd STW | 5920 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329499 | 351138 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EN | LL113EN | ll11 3en | ll113en | Wrexham | Wrecsam | Llanfynydd STW | 5970 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329262 | 351012 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EP | LL113EP | ll11 3ep | ll113ep | Wrexham | Wrecsam | Llanfynydd STW | 5729 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329246 | 351259 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EQ | LL113EQ | ll11 3eq | ll113eq | Wrexham | Wrecsam | Llanfynydd STW | 5557 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329191 | 351422 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3ER | LL113ER | ll11 3er | ll113er | Wrexham | Wrecsam | Llanfynydd STW | 5604 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329236 | 351386 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3ES | LL113ES | ll11 3es | ll113es | Wrexham | Wrecsam | Llanfynydd STW | 5813 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329054 | 351119 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3ET | LL113ET | ll11 3et | ll113et | Wrexham | Wrecsam | Llanfynydd STW | 5806 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329224 | 351172 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EU | LL113EU | ll11 3eu | ll113eu | Wrexham | Wrecsam | Llanfynydd STW | 5790 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329125 | 351161 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EW | LL113EW | ll11 3ew | ll113ew | Wrexham | Wrecsam | Llanfynydd STW | 5866 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329255 | 351118 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EX | LL113EX | ll11 3ex | ll113ex | Wrexham | Wrecsam | Llanfynydd STW | 5565 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328479 | 351254 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EY | LL113EY | ll11 3ey | ll113ey | Wrexham | Wrecsam | Llanfynydd STW | 5777 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329023 | 351148 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3EZ | LL113EZ | ll11 3ez | ll113ez | Wrexham | Wrecsam | Abenbury WwTW | 4974 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 331937 | 350249 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HA | LL113HA | ll11 3ha | ll113ha | Wrexham | Wrecsam | Llanfynydd STW | 5751 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328892 | 351143 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HB | LL113HB | ll11 3hb | ll113hb | Wrexham | Wrecsam | Llanfynydd STW | 5720 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329215 | 351259 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HD | LL113HD | ll11 3hd | ll113hd | Wrexham | Wrecsam | Llanfynydd STW | 5655 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329146 | 351307 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HE | LL113HE | ll11 3he | ll113he | Wrexham | Wrecsam | Llanfynydd STW | 5742 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329135 | 351213 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HF | LL113HF | ll11 3hf | ll113hf | Wrexham | Wrecsam | Llanfynydd STW | 5692 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329047 | 351242 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HG | LL113HG | ll11 3hg | ll113hg | Wrexham | Wrecsam | Llanfynydd STW | 5756 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329079 | 351184 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HH | LL113HH | ll11 3hh | ll113hh | Wrexham | Wrecsam | Llanfynydd STW | 5654 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329076 | 351289 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HJ | LL113HJ | ll11 3hj | ll113hj | Wrexham | Wrecsam | Llanfynydd STW | 5642 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328827 | 351241 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HL | LL113HL | ll11 3hl | ll113hl | Wrexham | Wrecsam | Llanfynydd STW | 5690 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328916 | 351212 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HN | LL113HN | ll11 3hn | ll113hn | Wrexham | Wrecsam | Llanfynydd STW | 5603 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328877 | 351292 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HP | LL113HP | ll11 3hp | ll113hp | Wrexham | Wrecsam | Llanfynydd STW | 5589 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329145 | 351375 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HR | LL113HR | ll11 3hr | ll113hr | Wrexham | Wrecsam | Llanfynydd STW | 5529 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328949 | 351385 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HS | LL113HS | ll11 3hs | ll113hs | Wrexham | Wrecsam | Llanfynydd STW | 5499 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328990 | 351426 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HT | LL113HT | ll11 3ht | ll113ht | Wrexham | Wrecsam | Llanfynydd STW | 5473 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328876 | 351425 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HU | LL113HU | ll11 3hu | ll113hu | Wrexham | Wrecsam | Llanfynydd STW | 5463 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328927 | 351448 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HW | LL113HW | ll11 3hw | ll113hw | Wrexham | Wrecsam | Llanfynydd STW | 5617 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328957 | 351296 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HX | LL113HX | ll11 3hx | ll113hx | Wrexham | Wrecsam | Llanfynydd STW | 5573 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328710 | 351287 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HY | LL113HY | ll11 3hy | ll113hy | Wrexham | Wrecsam | Llanfynydd STW | 5523 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329074 | 351424 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3HZ | LL113HZ | ll11 3hz | ll113hz | Wrexham | Wrecsam | Llanfynydd STW | 5656 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328796 | 351220 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LA | LL113LA | ll11 3la | ll113la | Wrexham | Wrecsam | Llanfynydd STW | 5448 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328915 | 351460 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LB | LL113LB | ll11 3lb | ll113lb | Wrexham | Wrecsam | Llanfynydd STW | 5506 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329162 | 351466 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LD | LL113LD | ll11 3ld | ll113ld | Wrexham | Wrecsam | Llanfynydd STW | 5470 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329148 | 351500 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LE | LL113LE | ll11 3le | ll113le | Wrexham | Wrecsam | Llanfynydd STW | 5484 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329121 | 351477 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LF | LL113LF | ll11 3lf | ll113lf | Wrexham | Wrecsam | Llanfynydd STW | 5307 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 328850 | 351589 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LG | LL113LG | ll11 3lg | ll113lg | Wrexham | Wrecsam | Llanfynydd STW | 5381 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329250 | 351624 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LH | LL113LH | ll11 3lh | ll113lh | Wrexham | Wrecsam | Llanfynydd STW | 5826 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328824 | 351052 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LJ | LL113LJ | ll11 3lj | ll113lj | Wrexham | Wrecsam | Llanfynydd STW | 5433 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328626 | 351413 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LL | LL113LL | ll11 3ll | ll113ll | Wrexham | Wrecsam | Llanfynydd STW | 5518 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329218 | 351470 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LN | LL113LN | ll11 3ln | ll113ln | Wrexham | Wrecsam | Llanfynydd STW | 5946 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329249 | 351034 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LP | LL113LP | ll11 3lp | ll113lp | Wrexham | Wrecsam | Llanfynydd STW | 5949 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329016 | 350969 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LQ | LL113LQ | ll11 3lq | ll113lq | Wrexham | Wrecsam | Llanfynydd STW | 5942 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328854 | 350940 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LR | LL113LR | ll11 3lr | ll113lr | Wrexham | Wrecsam | Llanfynydd STW | 5932 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328962 | 350974 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LS | LL113LS | ll11 3ls | ll113ls | Wrexham | Wrecsam | Llanfynydd STW | 5728 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328487 | 351090 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LT | LL113LT | ll11 3lt | ll113lt | Wrexham | Wrecsam | Llanfynydd STW | 6065 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329301 | 350925 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LU | LL113LU | ll11 3lu | ll113lu | Wrexham | Wrecsam | Llanfynydd STW | 5986 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329190 | 350976 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LW | LL113LW | ll11 3lw | ll113lw | Wrexham | Wrecsam | Llanfynydd STW | 5522 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328735 | 351344 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LX | LL113LX | ll11 3lx | ll113lx | Wrexham | Wrecsam | Llanfynydd STW | 4916 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327919 | 351845 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LY | LL113LY | ll11 3ly | ll113ly | Wrexham | Wrecsam | Llanfynydd STW | 5874 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328892 | 351017 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3LZ | LL113LZ | ll11 3lz | ll113lz | Wrexham | Wrecsam | Llanfynydd STW | 5967 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328949 | 350935 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NA | LL113NA | ll11 3na | ll113na | Wrexham | Wrecsam | Llanfynydd STW | 5789 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328624 | 351051 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NB | LL113NB | ll11 3nb | ll113nb | Wrexham | Wrecsam | Llanfynydd STW | 5748 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328554 | 351080 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3ND | LL113ND | ll11 3nd | ll113nd | Wrexham | Wrecsam | Llanfynydd STW | 5907 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329096 | 351032 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NE | LL113NE | ll11 3ne | ll113ne | Wrexham | Wrecsam | Llanfynydd STW | 5891 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329070 | 351042 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NG | LL113NG | ll11 3ng | ll113ng | Wrexham | Wrecsam | Llanfynydd STW | 5812 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328671 | 351036 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NJ | LL113NJ | ll11 3nj | ll113nj | Wrexham | Wrecsam | Llanfynydd STW | 6033 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329177 | 350923 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NL | LL113NL | ll11 3nl | ll113nl | Wrexham | Wrecsam | Llanfynydd STW | 5732 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328609 | 351106 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NN | LL113NN | ll11 3nn | ll113nn | Wrexham | Wrecsam | Llanfynydd STW | 5545 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329137 | 351419 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NP | LL113NP | ll11 3np | ll113np | Wrexham | Wrecsam | Llanfynydd STW | 6012 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329115 | 350929 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NQ | LL113NQ | ll11 3nq | ll113nq | Wrexham | Wrecsam | Llanfynydd STW | 5866 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329000 | 351051 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NR | LL113NR | ll11 3nr | ll113nr | Wrexham | Wrecsam | Llanfynydd STW | 5961 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329058 | 350967 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NS | LL113NS | ll11 3ns | ll113ns | Wrexham | Wrecsam | Llanfynydd STW | 5709 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328624 | 351132 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NT | LL113NT | ll11 3nt | ll113nt | Wrexham | Wrecsam | Llanfynydd STW | 5698 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328572 | 351134 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NU | LL113NU | ll11 3nu | ll113nu | Wrexham | Wrecsam | Llanfynydd STW | 5533 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328585 | 351304 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NW | LL113NW | ll11 3nw | ll113nw | Wrexham | Wrecsam | Llanfynydd STW | 5971 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329119 | 350972 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NX | LL113NX | ll11 3nx | ll113nx | Wrexham | Wrecsam | Llanfynydd STW | 5711 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328531 | 351114 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NY | LL113NY | ll11 3ny | ll113ny | Wrexham | Wrecsam | Llanfynydd STW | 5396 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328335 | 351403 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3NZ | LL113NZ | ll11 3nz | ll113nz | Wrexham | Wrecsam | Llanfynydd STW | 4883 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327848 | 351874 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PA | LL113PA | ll11 3pa | ll113pa | Wrexham | Wrecsam | Llanfynydd STW | 5527 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328556 | 351305 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PB | LL113PB | ll11 3pb | ll113pb | Wrexham | Wrecsam | Llanfynydd STW | 5337 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328416 | 351474 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PD | LL113PD | ll11 3pd | ll113pd | Wrexham | Wrecsam | Llanfynydd STW | 5151 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328346 | 351652 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PE | LL113PE | ll11 3pe | ll113pe | Wrexham | Wrecsam | Llanfynydd STW | 5327 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 328517 | 351501 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PF | LL113PF | ll11 3pf | ll113pf | Wrexham | Wrecsam | Llanfynydd STW | 5396 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328573 | 351441 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PG | LL113PG | ll11 3pg | ll113pg | Wrexham | Wrecsam | Llanfynydd STW | 5248 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 328530 | 351583 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PH | LL113PH | ll11 3ph | ll113ph | Wrexham | Wrecsam | Llanfynydd STW | 5042 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328247 | 351749 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PJ | LL113PJ | ll11 3pj | ll113pj | Wrexham | Wrecsam | Llanfynydd STW | 5131 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328016 | 351636 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PL | LL113PL | ll11 3pl | ll113pl | Wrexham | Wrecsam | Llanfynydd STW | 4984 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328101 | 351791 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PN | LL113PN | ll11 3pn | ll113pn | Wrexham | Wrecsam | Llanfynydd STW | 5025 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328229 | 351764 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PP | LL113PP | ll11 3pp | ll113pp | Wrexham | Wrecsam | Llanfynydd STW | 5266 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328337 | 351535 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PQ | LL113PQ | ll11 3pq | ll113pq | Wrexham | Wrecsam | Llanfynydd STW | 5319 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328279 | 351474 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PR | LL113PR | ll11 3pr | ll113pr | Wrexham | Wrecsam | Llanfynydd STW | 5243 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328216 | 351543 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PS | LL113PS | ll11 3ps | ll113ps | Wrexham | Wrecsam | Llanfynydd STW | 5187 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328208 | 351598 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PT | LL113PT | ll11 3pt | ll113pt | Wrexham | Wrecsam | Llanfynydd STW | 5085 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328185 | 351698 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PW | LL113PW | ll11 3pw | ll113pw | Wrexham | Wrecsam | Llanfynydd STW | 5515 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328432 | 351297 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PX | LL113PX | ll11 3px | ll113px | Wrexham | Wrecsam | Llanfynydd STW | 5168 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328108 | 351607 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PY | LL113PY | ll11 3py | ll113py | Wrexham | Wrecsam | Llanfynydd STW | 4893 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328005 | 351874 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3PZ | LL113PZ | ll11 3pz | ll113pz | Wrexham | Wrecsam | Llanfynydd STW | 5113 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328128 | 351664 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3QB | LL113QB | ll11 3qb | ll113qb | Wrexham | Wrecsam | Llanfynydd STW | 5363 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328381 | 351443 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RA | LL113RA | ll11 3ra | ll113ra | Wrexham | Wrecsam | Llanfynydd STW | 4926 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328057 | 351845 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RB | LL113RB | ll11 3rb | ll113rb | Wrexham | Wrecsam | Llanfynydd STW | 4921 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328107 | 351855 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RD | LL113RD | ll11 3rd | ll113rd | Wrexham | Wrecsam | Llanfynydd STW | 4744 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327804 | 352011 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RE | LL113RE | ll11 3re | ll113re | Wrexham | Wrecsam | Llanfynydd STW | 4906 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327879 | 351852 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RF | LL113RF | ll11 3rf | ll113rf | Wrexham | Wrecsam | Llanfynydd STW | 6002 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329062 | 350926 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RG | LL113RG | ll11 3rg | ll113rg | Wrexham | Wrecsam | Llanfynydd STW | 6013 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 329059 | 350914 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RH | LL113RH | ll11 3rh | ll113rh | Wrexham | Wrecsam | Llanfynydd STW | 4560 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327898 | 352200 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RJ | LL113RJ | ll11 3rj | ll113rj | Wrexham | Wrecsam | Llanfynydd STW | 6047 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328449 | 350762 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RL | LL113RL | ll11 3rl | ll113rl | Wrexham | Wrecsam | Llanfynydd STW | 5914 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328606 | 350921 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RN | LL113RN | ll11 3rn | ll113rn | Wrexham | Wrecsam | Llanfynydd STW | 5851 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328563 | 350977 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RP | LL113RP | ll11 3rp | ll113rp | Wrexham | Wrecsam | Llanfynydd STW | 5921 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328478 | 350893 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RR | LL113RR | ll11 3rr | ll113rr | Wrexham | Wrecsam | Llanfynydd STW | 5891 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328398 | 350913 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RS | LL113RS | ll11 3rs | ll113rs | Wrexham | Wrecsam | Llanfynydd STW | 5945 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328461 | 350867 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RT | LL113RT | ll11 3rt | ll113rt | Wrexham | Wrecsam | Llanfynydd STW | 5955 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328413 | 350850 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RU | LL113RU | ll11 3ru | ll113ru | Wrexham | Wrecsam | Llanfynydd STW | 5765 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328422 | 351043 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RW | LL113RW | ll11 3rw | ll113rw | Wrexham | Wrecsam | Llanfynydd STW | 6083 | 945 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.61 | 9.39 | 10.38 | 328514 | 350735 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3RY | LL113RY | ll11 3ry | ll113ry | Wrexham | Wrecsam | Llanfynydd STW | 5655 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328394 | 351150 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SA | LL113SA | ll11 3sa | ll113sa | Wrexham | Wrecsam | Llanfynydd STW | 5567 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328307 | 351227 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SB | LL113SB | ll11 3sb | ll113sb | Wrexham | Wrecsam | Llanfynydd STW | 5620 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328393 | 351185 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SD | LL113SD | ll11 3sd | ll113sd | Wrexham | Wrecsam | Llanfynydd STW | 5524 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328302 | 351270 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SE | LL113SE | ll11 3se | ll113se | Wrexham | Wrecsam | Llanfynydd STW | 5693 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328394 | 351112 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SF | LL113SF | ll11 3sf | ll113sf | Wrexham | Wrecsam | Llanfynydd STW | 5608 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328429 | 351203 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SG | LL113SG | ll11 3sg | ll113sg | Wrexham | Wrecsam | Llanfynydd STW | 5456 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328349 | 351345 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SH | LL113SH | ll11 3sh | ll113sh | Wrexham | Wrecsam | Llanfynydd STW | 5398 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327970 | 351365 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SL | LL113SL | ll11 3sl | ll113sl | Wrexham | Wrecsam | Llanfynydd STW | 5382 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328088 | 351390 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SN | LL113SN | ll11 3sn | ll113sn | Wrexham | Wrecsam | Llanfynydd STW | 5345 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327963 | 351418 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SP | LL113SP | ll11 3sp | ll113sp | Wrexham | Wrecsam | Llanfynydd STW | 5473 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328149 | 351304 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SR | LL113SR | ll11 3sr | ll113sr | Wrexham | Wrecsam | Llanfynydd STW | 5565 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328185 | 351216 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SS | LL113SS | ll11 3ss | ll113ss | Wrexham | Wrecsam | Llanfynydd STW | 5634 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328247 | 351153 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3ST | LL113ST | ll11 3st | ll113st | Wrexham | Wrecsam | Llanfynydd STW | 5705 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328204 | 351077 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SU | LL113SU | ll11 3su | ll113su | Wrexham | Wrecsam | Llanfynydd STW | 5693 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328282 | 351098 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SW | LL113SW | ll11 3sw | ll113sw | Wrexham | Wrecsam | Llanfynydd STW | 5408 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328026 | 351359 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3SY | LL113SY | ll11 3sy | ll113sy | Wrexham | Wrecsam | Llanfynydd STW | 5598 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328307 | 351196 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TA | LL113TA | ll11 3ta | ll113ta | Wrexham | Wrecsam | Llanfynydd STW | 5719 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328345 | 351079 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TB | LL113TB | ll11 3tb | ll113tb | Wrexham | Wrecsam | Llanfynydd STW | 5636 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328312 | 351159 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TD | LL113TD | ll11 3td | ll113td | Wrexham | Wrecsam | Llanfynydd STW | 5739 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328360 | 351061 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TE | LL113TE | ll11 3te | ll113te | Wrexham | Wrecsam | Llanfynydd STW | 5894 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328338 | 350902 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TF | LL113TF | ll11 3tf | ll113tf | Wrexham | Wrecsam | Llanfynydd STW | 6102 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328401 | 350700 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TG | LL113TG | ll11 3tg | ll113tg | Wrexham | Wrecsam | Llanfynydd STW | 5921 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328385 | 350881 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TH | LL113TH | ll11 3th | ll113th | Wrexham | Wrecsam | Llanfynydd STW | 6300 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328438 | 350505 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TJ | LL113TJ | ll11 3tj | ll113tj | Wrexham | Wrecsam | Llanfynydd STW | 5802 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328382 | 351000 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TL | LL113TL | ll11 3tl | ll113tl | Wrexham | Wrecsam | Llanfynydd STW | 6501 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 328625 | 350329 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TN | LL113TN | ll11 3tn | ll113tn | Wrexham | Wrecsam | Llanfynydd STW | 5959 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328321 | 350834 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TP | LL113TP | ll11 3tp | ll113tp | Wrexham | Wrecsam | Llanfynydd STW | 5838 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328232 | 350946 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TR | LL113TR | ll11 3tr | ll113tr | Wrexham | Wrecsam | Llanfynydd STW | 6183 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328404 | 350619 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TS | LL113TS | ll11 3ts | ll113ts | Wrexham | Wrecsam | Llanfynydd STW | 6431 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 328483 | 350379 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TT | LL113TT | ll11 3tt | ll113tt | Wrexham | Wrecsam | Llanfynydd STW | 6309 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 328359 | 350487 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TU | LL113TU | ll11 3tu | ll113tu | Wrexham | Wrecsam | Llanfynydd STW | 6307 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 328323 | 350484 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TW | LL113TW | ll11 3tw | ll113tw | Wrexham | Wrecsam | Llanfynydd STW | 6205 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328375 | 350593 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3TY | LL113TY | ll11 3ty | ll113ty | Wrexham | Wrecsam | Llanfynydd STW | 6503 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 328595 | 350323 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UA | LL113UA | ll11 3ua | ll113ua | Wrexham | Wrecsam | Llanfynydd STW | 6164 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328265 | 350622 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UB | LL113UB | ll11 3ub | ll113ub | Wrexham | Wrecsam | Llanfynydd STW | 5385 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328179 | 351396 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UD | LL113UD | ll11 3ud | ll113ud | Wrexham | Wrecsam | Llanfynydd STW | 5396 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328220 | 351389 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UE | LL113UE | ll11 3ue | ll113ue | Wrexham | Wrecsam | Llanfynydd STW | 5471 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328221 | 351314 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UF | LL113UF | ll11 3uf | ll113uf | Wrexham | Wrecsam | Llanfynydd STW | 5373 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328118 | 351402 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UG | LL113UG | ll11 3ug | ll113ug | Wrexham | Wrecsam | Llanfynydd STW | 5230 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327995 | 351535 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UH | LL113UH | ll11 3uh | ll113uh | Wrexham | Wrecsam | Llanfynydd STW | 5354 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328159 | 351425 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UL | LL113UL | ll11 3ul | ll113ul | Wrexham | Wrecsam | Llanfynydd STW | 5225 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328026 | 351543 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UN | LL113UN | ll11 3un | ll113un | Wrexham | Wrecsam | Llanfynydd STW | 5243 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327966 | 351520 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UQ | LL113UQ | ll11 3uq | ll113uq | Wrexham | Wrecsam | Llanfynydd STW | 5090 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327952 | 351673 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UR | LL113UR | ll11 3ur | ll113ur | Wrexham | Wrecsam | Llanfynydd STW | 5153 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327982 | 351611 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3US | LL113US | ll11 3us | ll113us | Wrexham | Wrecsam | Llanfynydd STW | 5106 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327885 | 351653 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UT | LL113UT | ll11 3ut | ll113ut | Wrexham | Wrecsam | Llanfynydd STW | 4437 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327597 | 352315 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3UW | LL113UW | ll11 3uw | ll113uw | Wrexham | Wrecsam | Llanfynydd STW | 5451 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 328280 | 351341 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YA | LL113YA | ll11 3ya | ll113ya | Wrexham | Wrecsam | Llanfynydd STW | 5032 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327897 | 351727 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YB | LL113YB | ll11 3yb | ll113yb | Wrexham | Wrecsam | Llanfynydd STW | 4996 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327949 | 351767 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YD | LL113YD | ll11 3yd | ll113yd | Wrexham | Wrecsam | Llanfynydd STW | 4905 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327346 | 351854 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YE | LL113YE | ll11 3ye | ll113ye | Wrexham | Wrecsam | Llanfynydd STW | 4975 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327441 | 351780 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YF | LL113YF | ll11 3yf | ll113yf | Wrexham | Wrecsam | Llanfynydd STW | 4921 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327218 | 351847 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YG | LL113YG | ll11 3yg | ll113yg | Wrexham | Wrecsam | Llanfynydd STW | 4869 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327248 | 351897 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YH | LL113YH | ll11 3yh | ll113yh | Wrexham | Wrecsam | Llanfynydd STW | 4842 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327324 | 351919 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YJ | LL113YJ | ll11 3yj | ll113yj | Wrexham | Wrecsam | Llanfynydd STW | 4876 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327213 | 351893 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YL | LL113YL | ll11 3yl | ll113yl | Wrexham | Wrecsam | Llanfynydd STW | 4780 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327254 | 351986 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YN | LL113YN | ll11 3yn | ll113yn | Wrexham | Wrecsam | Llanfynydd STW | 4907 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327147 | 351867 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YP | LL113YP | ll11 3yp | ll113yp | Wrexham | Wrecsam | Llanfynydd STW | 4711 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327178 | 352061 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YQ | LL113YQ | ll11 3yq | ll113yq | Wrexham | Wrecsam | Llanfynydd STW | 4659 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327453 | 352096 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YR | LL113YR | ll11 3yr | ll113yr | Wrexham | Wrecsam | Llanfynydd STW | 4475 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327412 | 352281 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YS | LL113YS | ll11 3ys | ll113ys | Wrexham | Wrecsam | Llanfynydd STW | 4263 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 326998 | 352534 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YT | LL113YT | ll11 3yt | ll113yt | Wrexham | Wrecsam | Llanfynydd STW | 4311 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327476 | 352443 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YU | LL113YU | ll11 3yu | ll113yu | Wrexham | Wrecsam | Llanfynydd STW | 4872 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327341 | 351888 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YW | LL113YW | ll11 3yw | ll113yw | Wrexham | Wrecsam | Llanfynydd STW | 4728 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327188 | 352043 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YY | LL113YY | ll11 3yy | ll113yy | Wrexham | Wrecsam | Llanfynydd STW | 5091 | 983 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.32 | 9.77 | 10.8 | 327834 | 351665 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 3YZ | LL113YZ | ll11 3yz | ll113yz | Wrexham | Wrecsam | Llanfynydd STW | 4815 | 1024 | 900to1200 | 2.05 | 1.5 | 1.1 | 19.09 | 10.18 | 11.25 | 327067 | 351968 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AA | LL114AA | ll11 4aa | ll114aa | Wrexham | Wrecsam | Gresford STW | 4123 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331733 | 353118 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AB | LL114AB | ll11 4ab | ll114ab | Wrexham | Wrecsam | Gresford STW | 4129 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331761 | 353076 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AD | LL114AD | ll11 4ad | ll114ad | Wrexham | Wrecsam | Gresford STW | 4053 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331830 | 353113 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AE | LL114AE | ll11 4ae | ll114ae | Wrexham | Wrecsam | Gresford STW | 4000 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331803 | 353227 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AF | LL114AF | ll11 4af | ll114af | Wrexham | Wrecsam | Gresford STW | 3871 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331650 | 353649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AG | LL114AG | ll11 4ag | ll114ag | Wrexham | Wrecsam | Gresford STW | 3118 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331972 | 354657 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AH | LL114AH | ll11 4ah | ll114ah | Wrexham | Wrecsam | Gresford STW | 3691 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331661 | 353977 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AJ | LL114AJ | ll11 4aj | ll114aj | Wrexham | Wrecsam | Gresford STW | 3538 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331946 | 353805 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AL | LL114AL | ll11 4al | ll114al | Wrexham | Wrecsam | Gresford STW | 3712 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331680 | 353902 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AN | LL114AN | ll11 4an | ll114an | Wrexham | Wrecsam | Gresford STW | 3703 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331675 | 353927 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AP | LL114AP | ll11 4ap | ll114ap | Wrexham | Wrecsam | Gresford STW | 3846 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331789 | 353494 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AQ | LL114AQ | ll11 4aq | ll114aq | Wrexham | Wrecsam | Gresford STW | 3972 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331973 | 353075 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AR | LL114AR | ll11 4ar | ll114ar | Wrexham | Wrecsam | Gresford STW | 3236 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332349 | 353766 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AS | LL114AS | ll11 4as | ll114as | Wrexham | Wrecsam | Gresford STW | 3860 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331804 | 353451 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AT | LL114AT | ll11 4at | ll114at | Wrexham | Wrecsam | Gresford STW | 3850 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331796 | 353478 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AW | LL114AW | ll11 4aw | ll114aw | Wrexham | Wrecsam | Gresford STW | 3685 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331657 | 353996 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AX | LL114AX | ll11 4ax | ll114ax | Wrexham | Wrecsam | Gresford STW | 4112 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332191 | 352671 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AY | LL114AY | ll11 4ay | ll114ay | Wrexham | Wrecsam | Gresford STW | 3194 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332411 | 353756 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4AZ | LL114AZ | ll11 4az | ll114az | Wrexham | Wrecsam | Gresford STW | 3282 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332410 | 353621 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BA | LL114BA | ll11 4ba | ll114ba | Wrexham | Wrecsam | Gresford STW | 2883 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332806 | 353779 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BB | LL114BB | ll11 4bb | ll114bb | Wrexham | Wrecsam | Gresford STW | 3164 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332466 | 353736 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BD | LL114BD | ll11 4bd | ll114bd | Wrexham | Wrecsam | Gresford STW | 3024 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332636 | 353755 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BE | LL114BE | ll11 4be | ll114be | Wrexham | Wrecsam | Gresford STW | 2993 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332706 | 353724 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BG | LL114BG | ll11 4bg | ll114bg | Wrexham | Wrecsam | Gresford STW | 3002 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332971 | 353464 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BH | LL114BH | ll11 4bh | ll114bh | Wrexham | Wrecsam | Gresford STW | 3088 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332524 | 353786 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BJ | LL114BJ | ll11 4bj | ll114bj | Wrexham | Wrecsam | Gresford STW | 2885 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332626 | 353981 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BL | LL114BL | ll11 4bl | ll114bl | Wrexham | Wrecsam | Gresford STW | 3049 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332510 | 353864 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BN | LL114BN | ll11 4bn | ll114bn | Wrexham | Wrecsam | Gresford STW | 2943 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332526 | 354015 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BP | LL114BP | ll11 4bp | ll114bp | Wrexham | Wrecsam | Gresford STW | 3153 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332367 | 353877 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BQ | LL114BQ | ll11 4bq | ll114bq | Wrexham | Wrecsam | Gresford STW | 2831 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332836 | 353822 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BS | LL114BS | ll11 4bs | ll114bs | Wrexham | Wrecsam | Gresford STW | 3123 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332370 | 353924 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BT | LL114BT | ll11 4bt | ll114bt | Wrexham | Wrecsam | Gresford STW | 3100 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332340 | 354005 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BU | LL114BU | ll11 4bu | ll114bu | Wrexham | Wrecsam | Gresford STW | 3005 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332463 | 353996 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BW | LL114BW | ll11 4bw | ll114bw | Wrexham | Wrecsam | Gresford STW | 3015 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332557 | 353859 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BX | LL114BX | ll11 4bx | ll114bx | Wrexham | Wrecsam | Gresford STW | 2872 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332681 | 353934 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BY | LL114BY | ll11 4by | ll114by | Wrexham | Wrecsam | Gresford STW | 2961 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332463 | 354072 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4BZ | LL114BZ | ll11 4bz | ll114bz | Wrexham | Wrecsam | Gresford STW | 3300 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332386 | 353621 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DA | LL114DA | ll11 4da | ll114da | Wrexham | Wrecsam | Gresford STW | 2923 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332555 | 354010 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DB | LL114DB | ll11 4db | ll114db | Wrexham | Wrecsam | Gresford STW | 2932 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332563 | 353985 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DD | LL114DD | ll11 4dd | ll114dd | Wrexham | Wrecsam | Gresford STW | 2716 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332598 | 354309 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DE | LL114DE | ll11 4de | ll114de | Wrexham | Wrecsam | Gresford STW | 3919 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331968 | 353159 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DF | LL114DF | ll11 4df | ll114df | Wrexham | Wrecsam | Gresford STW | 2429 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 332789 | 354546 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DG | LL114DG | ll11 4dg | ll114dg | Wrexham | Wrecsam | Gresford STW | 2784 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332796 | 353935 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DH | LL114DH | ll11 4dh | ll114dh | Wrexham | Wrecsam | Gresford STW | 2639 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332829 | 354121 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DJ | LL114DJ | ll11 4dj | ll114dj | Wrexham | Wrecsam | Gresford STW | 4106 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331693 | 353193 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DL | LL114DL | ll11 4dl | ll114dl | Wrexham | Wrecsam | Gresford STW | 2799 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332765 | 353948 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DN | LL114DN | ll11 4dn | ll114dn | Wrexham | Wrecsam | Gresford STW | 2755 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332716 | 354077 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DP | LL114DP | ll11 4dp | ll114dp | Wrexham | Wrecsam | Gresford STW | 4477 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331383 | 352987 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DQ | LL114DQ | ll11 4dq | ll114dq | Wrexham | Wrecsam | Gresford STW | 2926 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332684 | 353848 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DR | LL114DR | ll11 4dr | ll114dr | Wrexham | Wrecsam | Gresford STW | 4377 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331446 | 353068 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DS | LL114DS | ll11 4ds | ll114ds | Wrexham | Wrecsam | Gresford STW | 4211 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331620 | 353117 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DT | LL114DT | ll11 4dt | ll114dt | Wrexham | Wrecsam | Gresford STW | 4231 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331580 | 353134 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DU | LL114DU | ll11 4du | ll114du | Wrexham | Wrecsam | Gresford STW | 4127 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331677 | 353179 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DW | LL114DW | ll11 4dw | ll114dw | Wrexham | Wrecsam | Gresford STW | 2861 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332739 | 353884 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DX | LL114DX | ll11 4dx | ll114dx | Wrexham | Wrecsam | Gresford STW | 3269 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332141 | 353998 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DY | LL114DY | ll11 4dy | ll114dy | Wrexham | Wrecsam | Gresford STW | 4390 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331488 | 352996 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4DZ | LL114DZ | ll11 4dz | ll114dz | Wrexham | Wrecsam | Gresford STW | 3371 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332341 | 353564 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EA | LL114EA | ll11 4ea | ll114ea | Wrexham | Wrecsam | Gresford STW | 4234 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331658 | 353036 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EB | LL114EB | ll11 4eb | ll114eb | Wrexham | Wrecsam | Gresford STW | 4150 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331638 | 353191 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4ED | LL114ED | ll11 4ed | ll114ed | Wrexham | Wrecsam | Gresford STW | 4203 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331581 | 353178 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EE | LL114EE | ll11 4ee | ll114ee | Wrexham | Wrecsam | Gresford STW | 4223 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331512 | 353234 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EF | LL114EF | ll11 4ef | ll114ef | Wrexham | Wrecsam | Gresford STW | 4355 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331371 | 353203 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EG | LL114EG | ll11 4eg | ll114eg | Wrexham | Wrecsam | Gresford STW | 4289 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331514 | 353124 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EH | LL114EH | ll11 4eh | ll114eh | Wrexham | Wrecsam | Gresford STW | 4290 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331430 | 353233 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EJ | LL114EJ | ll11 4ej | ll114ej | Wrexham | Wrecsam | Gresford STW | 4298 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331389 | 353275 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EL | LL114EL | ll11 4el | ll114el | Wrexham | Wrecsam | Gresford STW | 4258 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331316 | 353452 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EN | LL114EN | ll11 4en | ll114en | Wrexham | Wrecsam | Gresford STW | 4196 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331265 | 353653 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EP | LL114EP | ll11 4ep | ll114ep | Wrexham | Wrecsam | Gresford STW | 4220 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331339 | 353487 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EQ | LL114EQ | ll11 4eq | ll114eq | Wrexham | Wrecsam | Gresford STW | 4035 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331728 | 353263 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4ER | LL114ER | ll11 4er | ll114er | Wrexham | Wrecsam | Gresford STW | 4157 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331322 | 353634 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4ES | LL114ES | ll11 4es | ll114es | Wrexham | Wrecsam | Gresford STW | 4141 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331267 | 353759 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4ET | LL114ET | ll11 4et | ll114et | Wrexham | Wrecsam | Gresford STW | 4296 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331278 | 353442 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EU | LL114EU | ll11 4eu | ll114eu | Wrexham | Wrecsam | Gresford STW | 4236 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331255 | 353592 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EW | LL114EW | ll11 4ew | ll114ew | Wrexham | Wrecsam | Gresford STW | 4233 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331390 | 353388 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EX | LL114EX | ll11 4ex | ll114ex | Wrexham | Wrecsam | Gresford STW | 4179 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331195 | 353812 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EY | LL114EY | ll11 4ey | ll114ey | Wrexham | Wrecsam | Gresford STW | 4185 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331446 | 353390 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4EZ | LL114EZ | ll11 4ez | ll114ez | Wrexham | Wrecsam | Gresford STW | 4158 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331574 | 353260 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4FA | LL114FA | ll11 4fa | ll114fa | Wrexham | Wrecsam | Gresford STW | 2989 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 332626 | 353818 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4FB | LL114FB | ll11 4fb | ll114fb | Wrexham | Wrecsam | Gresford STW | 4007 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332150 | 352849 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4FD | LL114FD | ll11 4fd | ll114fd | Wrexham | Wrecsam | Gresford STW | 4059 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332059 | 352864 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4FE | LL114FE | ll11 4fe | ll114fe | Wrexham | Wrecsam | Gresford STW | 3932 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332136 | 352966 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4FF | LL114FF | ll11 4ff | ll114ff | Wrexham | Wrecsam | Gresford STW | 3961 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332227 | 352841 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4FG | LL114FG | ll11 4fg | ll114fg | Wrexham | Wrecsam | Gresford STW | 3955 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332205 | 352869 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4FH | LL114FH | ll11 4fh | ll114fh | Wrexham | Wrecsam | Gresford STW | 4030 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332081 | 352883 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4FJ | LL114FJ | ll11 4fj | ll114fj | Wrexham | Wrecsam | Gresford STW | 4059 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331728 | 353225 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4FW | LL114FW | ll11 4fw | ll114fw | Wrexham | Wrecsam | Gresford STW | 3934 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332154 | 352946 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4GA | LL114GA | ll11 4ga | ll114ga | Wrexham | Wrecsam | Gresford STW | 3938 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332052 | 353042 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HA | LL114HA | ll11 4ha | ll114ha | Wrexham | Wrecsam | Gresford STW | 4159 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331466 | 353407 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HB | LL114HB | ll11 4hb | ll114hb | Wrexham | Wrecsam | Gresford STW | 4181 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331418 | 353439 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HD | LL114HD | ll11 4hd | ll114hd | Wrexham | Wrecsam | Gresford STW | 3884 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331658 | 353613 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HE | LL114HE | ll11 4he | ll114he | Wrexham | Wrecsam | Gresford STW | 4195 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331338 | 353535 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HF | LL114HF | ll11 4hf | ll114hf | Wrexham | Wrecsam | Gresford STW | 4151 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331348 | 353602 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HG | LL114HG | ll11 4hg | ll114hg | Wrexham | Wrecsam | Gresford STW | 4115 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331321 | 353718 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HH | LL114HH | ll11 4hh | ll114hh | Wrexham | Wrecsam | Gresford STW | 4069 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331342 | 353774 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HJ | LL114HJ | ll11 4hj | ll114hj | Wrexham | Wrecsam | Gresford STW | 3589 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332200 | 353395 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HL | LL114HL | ll11 4hl | ll114hl | Wrexham | Wrecsam | Gresford STW | 4028 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331364 | 353818 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HN | LL114HN | ll11 4hn | ll114hn | Wrexham | Wrecsam | Gresford STW | 4131 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331267 | 353781 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HP | LL114HP | ll11 4hp | ll114hp | Wrexham | Wrecsam | Gresford STW | 4106 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331245 | 353874 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HQ | LL114HQ | ll11 4hq | ll114hq | Wrexham | Wrecsam | Gresford STW | 4009 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331574 | 353514 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HR | LL114HR | ll11 4hr | ll114hr | Wrexham | Wrecsam | Gresford STW | 4046 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331299 | 353900 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HS | LL114HS | ll11 4hs | ll114hs | Wrexham | Wrecsam | Gresford STW | 4195 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331481 | 353324 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HT | LL114HT | ll11 4ht | ll114ht | Wrexham | Wrecsam | Gresford STW | 3907 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331902 | 353253 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HU | LL114HU | ll11 4hu | ll114hu | Wrexham | Wrecsam | Gresford STW | 4005 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331680 | 353374 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HW | LL114HW | ll11 4hw | ll114hw | Wrexham | Wrecsam | Gresford STW | 4063 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331314 | 353836 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HX | LL114HX | ll11 4hx | ll114hx | Wrexham | Wrecsam | Gresford STW | 4080 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331654 | 353284 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HY | LL114HY | ll11 4hy | ll114hy | Wrexham | Wrecsam | Gresford STW | 3707 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332083 | 353349 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4HZ | LL114HZ | ll11 4hz | ll114hz | Wrexham | Wrecsam | Gresford STW | 3964 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331750 | 353350 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4LA | LL114LA | ll11 4la | ll114la | Wrexham | Wrecsam | Gresford STW | 3756 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331988 | 353386 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4LB | LL114LB | ll11 4lb | ll114lb | Wrexham | Wrecsam | Gresford STW | 3800 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331918 | 353401 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4LD | LL114LD | ll11 4ld | ll114ld | Wrexham | Wrecsam | Gresford STW | 3797 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331941 | 353378 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4LE | LL114LE | ll11 4le | ll114le | Wrexham | Wrecsam | Gresford STW | 3764 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331875 | 353516 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4LG | LL114LG | ll11 4lg | ll114lg | Wrexham | Wrecsam | Gresford STW | 3805 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331976 | 353323 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4LN | LL114LN | ll11 4ln | ll114ln | Wrexham | Wrecsam | Gresford STW | 3751 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331852 | 353569 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4LS | LL114LS | ll11 4ls | ll114ls | Wrexham | Wrecsam | Gresford STW | 3698 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331771 | 353780 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4LW | LL114LW | ll11 4lw | ll114lw | Wrexham | Wrecsam | Gresford STW | 3745 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331886 | 353532 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4LY | LL114LY | ll11 4ly | ll114ly | Wrexham | Wrecsam | Gresford STW | 3609 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332022 | 353578 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NA | LL114NA | ll11 4na | ll114na | Wrexham | Wrecsam | Gresford STW | 3640 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331990 | 353569 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NB | LL114NB | ll11 4nb | ll114nb | Wrexham | Wrecsam | Gresford STW | 3694 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331924 | 353566 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4ND | LL114ND | ll11 4nd | ll114nd | Wrexham | Wrecsam | Gresford STW | 3738 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331833 | 353617 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NE | LL114NE | ll11 4ne | ll114ne | Wrexham | Wrecsam | Gresford STW | 3625 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332054 | 353512 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NF | LL114NF | ll11 4nf | ll114nf | Wrexham | Wrecsam | Gresford STW | 3604 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331816 | 353884 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NG | LL114NG | ll11 4ng | ll114ng | Wrexham | Wrecsam | Gresford STW | 3465 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331958 | 353920 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NH | LL114NH | ll11 4nh | ll114nh | Wrexham | Wrecsam | Gresford STW | 3681 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332067 | 353408 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NJ | LL114NJ | ll11 4nj | ll114nj | Wrexham | Wrecsam | Gresford STW | 3691 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332108 | 353345 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NL | LL114NL | ll11 4nl | ll114nl | Wrexham | Wrecsam | Gresford STW | 3636 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332134 | 353399 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NN | LL114NN | ll11 4nn | ll114nn | Wrexham | Wrecsam | Gresford STW | 3578 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332070 | 353567 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NP | LL114NP | ll11 4np | ll114np | Wrexham | Wrecsam | Gresford STW | 3730 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332126 | 353266 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NR | LL114NR | ll11 4nr | ll114nr | Wrexham | Wrecsam | Gresford STW | 3723 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332153 | 353247 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NS | LL114NS | ll11 4ns | ll114ns | Wrexham | Wrecsam | Gresford STW | 3734 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332114 | 353273 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NT | LL114NT | ll11 4nt | ll114nt | Wrexham | Wrecsam | Gresford STW | 3846 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332043 | 353185 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4NU | LL114NU | ll11 4nu | ll114nu | Wrexham | Wrecsam | Gresford STW | 3747 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332134 | 353233 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PB | LL114PB | ll11 4pb | ll114pb | Wrexham | Wrecsam | Gresford STW | 3690 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332217 | 353228 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PD | LL114PD | ll11 4pd | ll114pd | Wrexham | Wrecsam | Gresford STW | 3604 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332250 | 353317 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PE | LL114PE | ll11 4pe | ll114pe | Wrexham | Wrecsam | Gresford STW | 3623 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332272 | 353267 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PF | LL114PF | ll11 4pf | ll114pf | Wrexham | Wrecsam | Gresford STW | 3642 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332201 | 353314 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PG | LL114PG | ll11 4pg | ll114pg | Wrexham | Wrecsam | Gresford STW | 3574 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332694 | 352954 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PH | LL114PH | ll11 4ph | ll114ph | Wrexham | Wrecsam | Gresford STW | 3625 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332561 | 352996 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PJ | LL114PJ | ll11 4pj | ll114pj | Wrexham | Wrecsam | Gresford STW | 3659 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332640 | 352888 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PL | LL114PL | ll11 4pl | ll114pl | Wrexham | Wrecsam | Gresford STW | 3613 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332604 | 352975 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PN | LL114PN | ll11 4pn | ll114pn | Wrexham | Wrecsam | Gresford STW | 3533 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332775 | 352944 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PP | LL114PP | ll11 4pp | ll114pp | Wrexham | Wrecsam | Gresford STW | 3700 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332415 | 353022 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PQ | LL114PQ | ll11 4pq | ll114pq | Wrexham | Wrecsam | Gresford STW | 3724 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332410 | 352995 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PR | LL114PR | ll11 4pr | ll114pr | Wrexham | Wrecsam | Gresford STW | 3711 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332385 | 353035 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PS | LL114PS | ll11 4ps | ll114ps | Wrexham | Wrecsam | Gresford STW | 3703 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332406 | 353026 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PT | LL114PT | ll11 4pt | ll114pt | Wrexham | Wrecsam | Gresford STW | 3640 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332512 | 353017 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PW | LL114PW | ll11 4pw | ll114pw | Wrexham | Wrecsam | Gresford STW | 3491 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332841 | 352948 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PX | LL114PX | ll11 4px | ll114px | Wrexham | Wrecsam | Gresford STW | 3558 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332866 | 352848 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4PZ | LL114PZ | ll11 4pz | ll114pz | Wrexham | Wrecsam | Gresford STW | 3696 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332472 | 352978 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QA | LL114QA | ll11 4qa | ll114qa | Wrexham | Wrecsam | Gresford STW | 4415 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331147 | 353426 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QB | LL114QB | ll11 4qb | ll114qb | Wrexham | Wrecsam | Gresford STW | 4424 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331167 | 353378 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QD | LL114QD | ll11 4qd | ll114qd | Wrexham | Wrecsam | Hope WwTW | 4420 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330931 | 353689 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QE | LL114QE | ll11 4qe | ll114qe | Wrexham | Wrecsam | Gresford STW | 4508 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330955 | 353565 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QH | LL114QH | ll11 4qh | ll114qh | Wrexham | Wrecsam | Hope WwTW | 4482 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330920 | 353626 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QJ | LL114QJ | ll11 4qj | ll114qj | Wrexham | Wrecsam | Hope WwTW | 4421 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330950 | 353689 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QN | LL114QN | ll11 4qn | ll114qn | Wrexham | Wrecsam | Gresford STW | 3751 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332344 | 353018 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QR | LL114QR | ll11 4qr | ll114qr | Wrexham | Wrecsam | Gresford STW | 4193 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331856 | 352877 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QS | LL114QS | ll11 4qs | ll114qs | Wrexham | Wrecsam | Gresford STW | 4104 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332000 | 352858 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QT | LL114QT | ll11 4qt | ll114qt | Wrexham | Wrecsam | Gresford STW | 4507 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331424 | 352890 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QU | LL114QU | ll11 4qu | ll114qu | Wrexham | Wrecsam | Gresford STW | 4253 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331791 | 352859 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QW | LL114QW | ll11 4qw | ll114qw | Wrexham | Wrecsam | Gresford STW | 4300 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331811 | 352770 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QX | LL114QX | ll11 4qx | ll114qx | Wrexham | Wrecsam | Gresford STW | 4296 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331861 | 352726 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QY | LL114QY | ll11 4qy | ll114qy | Wrexham | Wrecsam | Gresford STW | 4242 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331746 | 352923 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4QZ | LL114QZ | ll11 4qz | ll114qz | Wrexham | Wrecsam | Gresford STW | 4224 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331837 | 352853 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RA | LL114RA | ll11 4ra | ll114ra | Wrexham | Wrecsam | Gresford STW | 3534 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332825 | 352907 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RB | LL114RB | ll11 4rb | ll114rb | Wrexham | Wrecsam | Gresford STW | 3445 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333075 | 352847 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RE | LL114RE | ll11 4re | ll114re | Wrexham | Wrecsam | Gresford STW | 3808 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332900 | 352529 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RF | LL114RF | ll11 4rf | ll114rf | Wrexham | Wrecsam | Gresford STW | 3449 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332939 | 352931 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RG | LL114RG | ll11 4rg | ll114rg | Wrexham | Wrecsam | Gresford STW | 3454 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332853 | 352985 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RH | LL114RH | ll11 4rh | ll114rh | Wrexham | Wrecsam | Gresford STW | 4076 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331973 | 352925 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RJ | LL114RJ | ll11 4rj | ll114rj | Wrexham | Wrecsam | Gresford STW | 3500 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333062 | 352791 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RL | LL114RL | ll11 4rl | ll114rl | Wrexham | Wrecsam | Gresford STW | 3597 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332962 | 352739 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RN | LL114RN | ll11 4rn | ll114rn | Wrexham | Wrecsam | Gresford STW | 3550 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333003 | 352768 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RP | LL114RP | ll11 4rp | ll114rp | Wrexham | Wrecsam | Gresford STW | 3637 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332961 | 352692 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RQ | LL114RQ | ll11 4rq | ll114rq | Wrexham | Wrecsam | Gresford STW | 3564 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331974 | 353719 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RR | LL114RR | ll11 4rr | ll114rr | Wrexham | Wrecsam | Gresford STW | 3592 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331910 | 353762 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RS | LL114RS | ll11 4rs | ll114rs | Wrexham | Wrecsam | Gresford STW | 3704 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331839 | 353667 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RT | LL114RT | ll11 4rt | ll114rt | Wrexham | Wrecsam | Gresford STW | 3677 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331812 | 353756 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RU | LL114RU | ll11 4ru | ll114ru | Wrexham | Wrecsam | Gresford STW | 3630 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331826 | 353821 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RW | LL114RW | ll11 4rw | ll114rw | Wrexham | Wrecsam | Gresford STW | 3569 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332991 | 352753 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RX | LL114RX | ll11 4rx | ll114rx | Wrexham | Wrecsam | Gresford STW | 3553 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332073 | 353603 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4RY | LL114RY | ll11 4ry | ll114ry | Wrexham | Wrecsam | Gresford STW | 3498 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331999 | 353798 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SB | LL114SB | ll11 4sb | ll114sb | Wrexham | Wrecsam | Gresford STW | 4185 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331886 | 352858 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SD | LL114SD | ll11 4sd | ll114sd | Wrexham | Wrecsam | Gresford STW | 4162 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331944 | 352832 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SE | LL114SE | ll11 4se | ll114se | Wrexham | Wrecsam | Gresford STW | 4156 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331938 | 352847 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SF | LL114SF | ll11 4sf | ll114sf | Wrexham | Wrecsam | Gresford STW | 4433 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331378 | 353065 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SG | LL114SG | ll11 4sg | ll114sg | Wrexham | Wrecsam | Gresford STW | 4520 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331349 | 352961 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SH | LL114SH | ll11 4sh | ll114sh | Wrexham | Wrecsam | Gresford STW | 4591 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331351 | 352846 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SJ | LL114SJ | ll11 4sj | ll114sj | Wrexham | Wrecsam | Gresford STW | 4135 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331798 | 353025 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SL | LL114SL | ll11 4sl | ll114sl | Wrexham | Wrecsam | Gresford STW | 4642 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331311 | 352815 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SP | LL114SP | ll11 4sp | ll114sp | Wrexham | Wrecsam | Gresford STW | 4462 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331176 | 353295 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SQ | LL114SQ | ll11 4sq | ll114sq | Wrexham | Wrecsam | Gresford STW | 4227 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331745 | 352947 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SR | LL114SR | ll11 4sr | ll114sr | Wrexham | Wrecsam | Gresford STW | 4393 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331052 | 353627 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SS | LL114SS | ll11 4ss | ll114ss | Wrexham | Wrecsam | Gresford STW | 4388 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331038 | 353663 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4ST | LL114ST | ll11 4st | ll114st | Wrexham | Wrecsam | Hope WwTW | 4372 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330922 | 353736 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SU | LL114SU | ll11 4su | ll114su | Wrexham | Wrecsam | Hope WwTW | 4403 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330990 | 353711 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SW | LL114SW | ll11 4sw | ll114sw | Wrexham | Wrecsam | Gresford STW | 4516 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331344 | 352973 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SX | LL114SX | ll11 4sx | ll114sx | Wrexham | Wrecsam | Gresford STW | 4362 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331937 | 352562 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SY | LL114SY | ll11 4sy | ll114sy | Wrexham | Wrecsam | Hope WwTW | 4030 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331156 | 354107 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4SZ | LL114SZ | ll11 4sz | ll114sz | Wrexham | Wrecsam | Gresford STW | 4390 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331836 | 352619 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TA | LL114TA | ll11 4ta | ll114ta | Wrexham | Wrecsam | Hope WwTW | 4283 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330931 | 353826 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TB | LL114TB | ll11 4tb | ll114tb | Wrexham | Wrecsam | Hope WwTW | 4227 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330902 | 353880 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TD | LL114TD | ll11 4td | ll114td | Wrexham | Wrecsam | Hope WwTW | 4264 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330945 | 353847 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TE | LL114TE | ll11 4te | ll114te | Wrexham | Wrecsam | Hope WwTW | 4248 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330944 | 353863 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TF | LL114TF | ll11 4tf | ll114tf | Wrexham | Wrecsam | Gresford STW | 4608 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331362 | 352806 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TG | LL114TG | ll11 4tg | ll114tg | Wrexham | Wrecsam | Hope WwTW | 3748 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330794 | 354352 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TH | LL114TH | ll11 4th | ll114th | Wrexham | Wrecsam | Gresford STW | 4120 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 332013 | 352823 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TJ | LL114TJ | ll11 4tj | ll114tj | Wrexham | Wrecsam | Gresford STW | 4441 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331796 | 352586 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TL | LL114TL | ll11 4tl | ll114tl | Wrexham | Wrecsam | Gresford STW | 4340 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331118 | 353619 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TN | LL114TN | ll11 4tn | ll114tn | Wrexham | Wrecsam | Gresford STW | 4316 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331160 | 353594 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TP | LL114TP | ll11 4tp | ll114tp | Wrexham | Wrecsam | Gresford STW | 4200 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331114 | 353924 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TQ | LL114TQ | ll11 4tq | ll114tq | Wrexham | Wrecsam | Gresford STW | 4296 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331910 | 352678 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TR | LL114TR | ll11 4tr | ll114tr | Wrexham | Wrecsam | Hope WwTW | 4061 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331032 | 354060 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TS | LL114TS | ll11 4ts | ll114ts | Wrexham | Wrecsam | Hope WwTW | 3730 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330946 | 354383 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TT | LL114TT | ll11 4tt | ll114tt | Wrexham | Wrecsam | Gresford STW | 4345 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331223 | 353436 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TU | LL114TU | ll11 4tu | ll114tu | Wrexham | Wrecsam | Hope WwTW | 3769 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331167 | 354373 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TW | LL114TW | ll11 4tw | ll114tw | Wrexham | Wrecsam | Gresford STW | 4256 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331109 | 353811 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TX | LL114TX | ll11 4tx | ll114tx | Wrexham | Wrecsam | Gresford STW | 4344 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331083 | 353673 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TY | LL114TY | ll11 4ty | ll114ty | Wrexham | Wrecsam | Hope WwTW | 4165 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331009 | 353952 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4TZ | LL114TZ | ll11 4tz | ll114tz | Wrexham | Wrecsam | Hope WwTW | 4153 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330945 | 353958 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UA | LL114UA | ll11 4ua | ll114ua | Wrexham | Wrecsam | Gresford STW | 4324 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331058 | 353761 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UB | LL114UB | ll11 4ub | ll114ub | Wrexham | Wrecsam | Gresford STW | 4256 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331163 | 353711 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UD | LL114UD | ll11 4ud | ll114ud | Wrexham | Wrecsam | Gresford STW | 4335 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331198 | 353495 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UE | LL114UE | ll11 4ue | ll114ue | Wrexham | Wrecsam | Gresford STW | 4401 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331283 | 353247 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UF | LL114UF | ll11 4uf | ll114uf | Wrexham | Wrecsam | Gresford STW | 4135 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331195 | 353908 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UG | LL114UG | ll11 4ug | ll114ug | Wrexham | Wrecsam | Gresford STW | 3992 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331301 | 354015 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UH | LL114UH | ll11 4uh | ll114uh | Wrexham | Wrecsam | Gresford STW | 4043 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331215 | 354076 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UJ | LL114UJ | ll11 4uj | ll114uj | Wrexham | Wrecsam | Gresford STW | 4462 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331525 | 352841 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UL | LL114UL | ll11 4ul | ll114ul | Wrexham | Wrecsam | Hope WwTW | 4080 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330956 | 354032 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UN | LL114UN | ll11 4un | ll114un | Wrexham | Wrecsam | Gresford STW | 4592 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331482 | 352694 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UP | LL114UP | ll11 4up | ll114up | Wrexham | Wrecsam | Gresford STW | 4530 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331203 | 353136 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UQ | LL114UQ | ll11 4uq | ll114uq | Wrexham | Wrecsam | Gresford STW | 4422 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331630 | 352784 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UR | LL114UR | ll11 4ur | ll114ur | Wrexham | Wrecsam | Gresford STW | 4817 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331493 | 352357 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4US | LL114US | ll11 4us | ll114us | Wrexham | Wrecsam | Gresford STW | 4938 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331503 | 352179 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UT | LL114UT | ll11 4ut | ll114ut | Wrexham | Wrecsam | Gresford STW | 4934 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331547 | 352144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UU | LL114UU | ll11 4uu | ll114uu | Wrexham | Wrecsam | Gresford STW | 4932 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331553 | 352141 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UW | LL114UW | ll11 4uw | ll114uw | Wrexham | Wrecsam | Gresford STW | 4549 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331525 | 352710 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UX | LL114UX | ll11 4ux | ll114ux | Wrexham | Wrecsam | Gresford STW | 4511 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331452 | 352850 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UY | LL114UY | ll11 4uy | ll114uy | Wrexham | Wrecsam | Gresford STW | 4936 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331562 | 352128 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4UZ | LL114UZ | ll11 4uz | ll114uz | Wrexham | Wrecsam | Gresford STW | 4350 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331616 | 352907 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4XA | LL114XA | ll11 4xa | ll114xa | Wrexham | Wrecsam | Gresford STW | 4409 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331543 | 352901 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4XB | LL114XB | ll11 4xb | ll114xb | Wrexham | Wrecsam | Gresford STW | 4598 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331532 | 352630 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4XD | LL114XD | ll11 4xd | ll114xd | Wrexham | Wrecsam | Gresford STW | 4480 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331657 | 352671 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4XE | LL114XE | ll11 4xe | ll114xe | Wrexham | Wrecsam | Gresford STW | 4564 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331597 | 352612 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4XF | LL114XF | ll11 4xf | ll114xf | Wrexham | Wrecsam | Gresford STW | 4451 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331613 | 352759 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4XG | LL114XG | ll11 4xg | ll114xg | Wrexham | Wrecsam | Gresford STW | 4413 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331763 | 352658 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4XQ | LL114XQ | ll11 4xq | ll114xq | Wrexham | Wrecsam | Gresford STW | 4333 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331762 | 352773 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YA | LL114YA | ll11 4ya | ll114ya | Wrexham | Wrecsam | Gresford STW | 4931 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331579 | 352119 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YB | LL114YB | ll11 4yb | ll114yb | Wrexham | Wrecsam | Gresford STW | 4998 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331483 | 352116 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YD | LL114YD | ll11 4yd | ll114yd | Wrexham | Wrecsam | Gresford STW | 5004 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331495 | 352097 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YE | LL114YE | ll11 4ye | ll114ye | Wrexham | Wrecsam | Gresford STW | 5148 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331888 | 351593 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YF | LL114YF | ll11 4yf | ll114yf | Wrexham | Wrecsam | Gresford STW | 4660 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 332171 | 351990 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YG | LL114YG | ll11 4yg | ll114yg | Wrexham | Wrecsam | Gresford STW | 4482 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331957 | 352384 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YH | LL114YH | ll11 4yh | ll114yh | Wrexham | Wrecsam | Gresford STW | 4307 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 332442 | 352231 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YJ | LL114YJ | ll11 4yj | ll114yj | Wrexham | Wrecsam | Gresford STW | 4571 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331659 | 352539 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YL | LL114YL | ll11 4yl | ll114yl | Wrexham | Wrecsam | Gresford STW | 3882 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332810 | 352497 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YN | LL114YN | ll11 4yn | ll114yn | Wrexham | Wrecsam | Gresford STW | 3905 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331339 | 354138 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YP | LL114YP | ll11 4yp | ll114yp | Wrexham | Wrecsam | Gresford STW | 4603 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331640 | 352513 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YQ | LL114YQ | ll11 4yq | ll114yq | Wrexham | Wrecsam | Gresford STW | 4559 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331715 | 352501 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YR | LL114YR | ll11 4yr | ll114yr | Wrexham | Wrecsam | Gresford STW | 4647 | 835 | 700to900 | 1.67 | 1.22 | 0.9 | 15.56 | 8.3 | 9.17 | 331555 | 352536 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YS | LL114YS | ll11 4ys | ll114ys | Wrexham | Wrecsam | Gresford STW | 4665 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331621 | 352444 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YT | LL114YT | ll11 4yt | ll114yt | Wrexham | Wrecsam | Gresford STW | 4612 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331690 | 352452 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YU | LL114YU | ll11 4yu | ll114yu | Wrexham | Wrecsam | Gresford STW | 4490 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331848 | 352471 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YW | LL114YW | ll11 4yw | ll114yw | Wrexham | Wrecsam | Gresford STW | 4719 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331935 | 352095 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YX | LL114YX | ll11 4yx | ll114yx | Wrexham | Wrecsam | Gresford STW | 4404 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 331109 | 353509 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YY | LL114YY | ll11 4yy | ll114yy | Wrexham | Wrecsam | Gresford STW | 3803 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332796 | 352600 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4YZ | LL114YZ | ll11 4yz | ll114yz | Wrexham | Wrecsam | Gresford STW | 3937 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332806 | 352435 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 4ZA | LL114ZA | ll11 4za | ll114za | Wrexham | Wrecsam | Gresford STW | 3911 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332789 | 352476 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AA | LL115AA | ll11 5aa | ll115aa | Wrexham | Wrecsam | Llanfynydd STW | 3288 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329368 | 353966 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AB | LL115AB | ll11 5ab | ll115ab | Wrexham | Wrecsam | Llanfynydd STW | 3303 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329316 | 353917 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AD | LL115AD | ll11 5ad | ll115ad | Wrexham | Wrecsam | Llanfynydd STW | 3301 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329288 | 353903 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AE | LL115AE | ll11 5ae | ll115ae | Wrexham | Wrecsam | Llanfynydd STW | 3358 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329161 | 353768 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AF | LL115AF | ll11 5af | ll115af | Wrexham | Wrecsam | Llanfynydd STW | 3431 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329043 | 353629 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AG | LL115AG | ll11 5ag | ll115ag | Wrexham | Wrecsam | Llanfynydd STW | 3169 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329175 | 353990 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AH | LL115AH | ll11 5ah | ll115ah | Wrexham | Wrecsam | Llanfynydd STW | 3095 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329097 | 354031 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AJ | LL115AJ | ll11 5aj | ll115aj | Wrexham | Wrecsam | Llanfynydd STW | 3190 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329327 | 354056 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AL | LL115AL | ll11 5al | ll115al | Wrexham | Wrecsam | Llanfynydd STW | 3230 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329077 | 353868 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AN | LL115AN | ll11 5an | ll115an | Wrexham | Wrecsam | Llanfynydd STW | 3064 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329010 | 354021 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AP | LL115AP | ll11 5ap | ll115ap | Wrexham | Wrecsam | Llanfynydd STW | 3047 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 328971 | 354020 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AQ | LL115AQ | ll11 5aq | ll115aq | Wrexham | Wrecsam | Llanfynydd STW | 4505 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 325616 | 352717 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AR | LL115AR | ll11 5ar | ll115ar | Wrexham | Wrecsam | Llanfynydd STW | 2935 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329029 | 354176 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AS | LL115AS | ll11 5as | ll115as | Wrexham | Wrecsam | Llanfynydd STW | 3263 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329044 | 353815 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AT | LL115AT | ll11 5at | ll115at | Wrexham | Wrecsam | Llanfynydd STW | 3332 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329087 | 353760 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AU | LL115AU | ll11 5au | ll115au | Wrexham | Wrecsam | Llanfynydd STW | 3338 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329131 | 353775 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AW | LL115AW | ll11 5aw | ll115aw | Wrexham | Wrecsam | Llanfynydd STW | 3069 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329034 | 354027 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AX | LL115AX | ll11 5ax | ll115ax | Wrexham | Wrecsam | Llanfynydd STW | 3741 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329498 | 353516 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5AY | LL115AY | ll11 5ay | ll115ay | Wrexham | Wrecsam | Llanfynydd STW | 3377 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329250 | 353794 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BA | LL115BA | ll11 5ba | ll115ba | Wrexham | Wrecsam | Llanfynydd STW | 3426 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329220 | 353722 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BB | LL115BB | ll11 5bb | ll115bb | Wrexham | Wrecsam | Llanfynydd STW | 3501 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329281 | 353669 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BD | LL115BD | ll11 5bd | ll115bd | Wrexham | Wrecsam | Llanfynydd STW | 3392 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329318 | 353815 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BH | LL115BH | ll11 5bh | ll115bh | Wrexham | Wrecsam | Llanfynydd STW | 3741 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329789 | 353704 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BJ | LL115BJ | ll11 5bj | ll115bj | Wrexham | Wrecsam | Llanfynydd STW | 3818 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 325944 | 353321 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BL | LL115BL | ll11 5bl | ll115bl | Wrexham | Wrecsam | Llanfynydd STW | 3400 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329461 | 353893 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BN | LL115BN | ll11 5bn | ll115bn | Wrexham | Wrecsam | Llanfynydd STW | 3280 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329524 | 354080 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BP | LL115BP | ll11 5bp | ll115bp | Wrexham | Wrecsam | Llanfynydd STW | 3443 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329507 | 353871 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BQ | LL115BQ | ll11 5bq | ll115bq | Wrexham | Wrecsam | Llanfynydd STW | 3359 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329396 | 353900 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BT | LL115BT | ll11 5bt | ll115bt | Wrexham | Wrecsam | Llanfynydd STW | 3592 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329461 | 353667 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BU | LL115BU | ll11 5bu | ll115bu | Wrexham | Wrecsam | Llanfynydd STW | 3320 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329524 | 354032 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BW | LL115BW | ll11 5bw | ll115bw | Wrexham | Wrecsam | Llanfynydd STW | 3445 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329468 | 353844 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5BY | LL115BY | ll11 5by | ll115by | Wrexham | Wrecsam | Llanfynydd STW | 3507 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329468 | 353771 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DA | LL115DA | ll11 5da | ll115da | Wrexham | Wrecsam | Llanfynydd STW | 3295 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329438 | 354003 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DB | LL115DB | ll11 5db | ll115db | Wrexham | Wrecsam | Llanfynydd STW | 3237 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329365 | 354025 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DD | LL115DD | ll11 5dd | ll115dd | Wrexham | Wrecsam | Llanfynydd STW | 3155 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329358 | 354118 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DE | LL115DE | ll11 5de | ll115de | Wrexham | Wrecsam | Llanfynydd STW | 3173 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329344 | 354087 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DF | LL115DF | ll11 5df | ll115df | Wrexham | Wrecsam | Llanfynydd STW | 3141 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329380 | 354150 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DG | LL115DG | ll11 5dg | ll115dg | Wrexham | Wrecsam | Llanfynydd STW | 3190 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329349 | 354071 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DH | LL115DH | ll11 5dh | ll115dh | Wrexham | Wrecsam | Llanfynydd STW | 3231 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329480 | 354109 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DJ | LL115DJ | ll11 5dj | ll115dj | Wrexham | Wrecsam | Llanfynydd STW | 3382 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329597 | 354008 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DL | LL115DL | ll11 5dl | ll115dl | Wrexham | Wrecsam | Llanfynydd STW | 3210 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329455 | 354117 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DN | LL115DN | ll11 5dn | ll115dn | Wrexham | Wrecsam | Llanfynydd STW | 3280 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329499 | 354063 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DP | LL115DP | ll11 5dp | ll115dp | Wrexham | Wrecsam | Llanfynydd STW | 3373 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329659 | 354065 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DQ | LL115DQ | ll11 5dq | ll115dq | Wrexham | Wrecsam | Llanfynydd STW | 3332 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329819 | 354248 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DR | LL115DR | ll11 5dr | ll115dr | Wrexham | Wrecsam | Llanfynydd STW | 3362 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329798 | 354190 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DS | LL115DS | ll11 5ds | ll115ds | Wrexham | Wrecsam | Llanfynydd STW | 3475 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329638 | 353922 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DT | LL115DT | ll11 5dt | ll115dt | Wrexham | Wrecsam | Llanfynydd STW | 3476 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329786 | 354033 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DU | LL115DU | ll11 5du | ll115du | Wrexham | Wrecsam | Llanfynydd STW | 3448 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329685 | 353990 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DW | LL115DW | ll11 5dw | ll115dw | Wrexham | Wrecsam | Llanfynydd STW | 2894 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329384 | 354457 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DX | LL115DX | ll11 5dx | ll115dx | Wrexham | Wrecsam | Llanfynydd STW | 3553 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329754 | 353911 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DY | LL115DY | ll11 5dy | ll115dy | Wrexham | Wrecsam | Llanfynydd STW | 3604 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329743 | 353839 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5DZ | LL115DZ | ll11 5dz | ll115dz | Wrexham | Wrecsam | Llanfynydd STW | 3597 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329639 | 353775 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5EA | LL115EA | ll11 5ea | ll115ea | Wrexham | Wrecsam | Llanfynydd STW | 3479 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329598 | 353889 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5EB | LL115EB | ll11 5eb | ll115eb | Wrexham | Wrecsam | Llanfynydd STW | 3214 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 329243 | 353977 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5ED | LL115ED | ll11 5ed | ll115ed | Wrexham | Wrecsam | Llanfynydd STW | 3619 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329733 | 353813 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5EE | LL115EE | ll11 5ee | ll115ee | Wrexham | Wrecsam | Llanfynydd STW | 3596 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329606 | 353754 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5EF | LL115EF | ll11 5ef | ll115ef | Flintshire | Sir Y Fflint | Llanfynydd STW | 1685 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 328562 | 355353 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5EG | LL115EG | ll11 5eg | ll115eg | Flintshire | Sir Y Fflint | Llanfynydd STW | 1646 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 328537 | 355384 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5EH | LL115EH | ll11 5eh | ll115eh | Flintshire | Sir Y Fflint | Llanfynydd STW | 1524 | 965 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.99 | 9.59 | 10.6 | 328447 | 355470 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5EJ | LL115EJ | ll11 5ej | ll115ej | Wrexham | Wrecsam | Llanfynydd STW | 3433 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329585 | 353936 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5EL | LL115EL | ll11 5el | ll115el | Flintshire | Sir Y Fflint | Llanfynydd STW | 2148 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 329030 | 355131 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5EN | LL115EN | ll11 5en | ll115en | Flintshire | Sir Y Fflint | Llanfynydd STW | 1630 | 933 | 900to1200 | 1.87 | 1.37 | 1 | 17.39 | 9.27 | 10.25 | 328859 | 355691 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5EP | LL115EP | ll11 5ep | ll115ep | Flintshire | Sir Y Fflint | Llanfynydd STW | 2036 | 933 | 900to1200 | 1.87 | 1.37 | 1 | 17.39 | 9.27 | 10.25 | 329421 | 355802 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5EQ | LL115EQ | ll11 5eq | ll115eq | Wrexham | Wrecsam | Llanfynydd STW | 3557 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329556 | 353768 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5ER | LL115ER | ll11 5er | ll115er | Flintshire | Sir Y Fflint | Llanfynydd STW | 1839 | 933 | 900to1200 | 1.87 | 1.37 | 1 | 17.39 | 9.27 | 10.25 | 329207 | 355823 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5ES | LL115ES | ll11 5es | ll115es | Flintshire | Sir Y Fflint | Llanfynydd STW | 2295 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 329612 | 355611 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5ET | LL115ET | ll11 5et | ll115et | Flintshire | Sir Y Fflint | Llanfynydd STW | 2553 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329525 | 355051 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5EU | LL115EU | ll11 5eu | ll115eu | Flintshire | Sir Y Fflint | Llanfynydd STW | 2205 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 329678 | 355961 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5EW | LL115EW | ll11 5ew | ll115ew | Flintshire | Sir Y Fflint | Llanfynydd STW | 2081 | 933 | 900to1200 | 1.87 | 1.37 | 1 | 17.39 | 9.27 | 10.25 | 329438 | 355738 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5EX | LL115EX | ll11 5ex | ll115ex | Wrexham | Wrecsam | Llanfynydd STW | 3573 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329594 | 353773 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5EY | LL115EY | ll11 5ey | ll115ey | Flintshire | Sir Y Fflint | Llanfynydd STW | 2118 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 329636 | 356103 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5EZ | LL115EZ | ll11 5ez | ll115ez | Wrexham | Wrecsam | Llanfynydd STW | 3500 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329570 | 353845 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FB | LL115FB | ll11 5fb | ll115fb | Wrexham | Wrecsam | Llanfynydd STW | 4607 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329610 | 352597 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FD | LL115FD | ll11 5fd | ll115fd | Wrexham | Wrecsam | Llanfynydd STW | 4590 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329679 | 352650 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FE | LL115FE | ll11 5fe | ll115fe | Wrexham | Wrecsam | Llanfynydd STW | 4526 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329583 | 352673 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FF | LL115FF | ll11 5ff | ll115ff | Wrexham | Wrecsam | Llanfynydd STW | 4400 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329648 | 352847 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FG | LL115FG | ll11 5fg | ll115fg | Wrexham | Wrecsam | Llanfynydd STW | 4492 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329680 | 352760 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FH | LL115FH | ll11 5fh | ll115fh | Wrexham | Wrecsam | Llanfynydd STW | 4378 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329720 | 352910 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FJ | LL115FJ | ll11 5fj | ll115fj | Wrexham | Wrecsam | Llanfynydd STW | 4409 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 329470 | 352750 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FL | LL115FL | ll11 5fl | ll115fl | Wrexham | Wrecsam | Llanfynydd STW | 4326 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 329480 | 352846 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FN | LL115FN | ll11 5fn | ll115fn | Wrexham | Wrecsam | Llanfynydd STW | 4296 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 329418 | 352850 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FP | LL115FP | ll11 5fp | ll115fp | Wrexham | Wrecsam | Llanfynydd STW | 4266 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 329492 | 352918 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FQ | LL115FQ | ll11 5fq | ll115fq | Wrexham | Wrecsam | Llanfynydd STW | 4135 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 329437 | 353037 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FS | LL115FS | ll11 5fs | ll115fs | Wrexham | Wrecsam | Llanfynydd STW | 4086 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329530 | 353140 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FT | LL115FT | ll11 5ft | ll115ft | Wrexham | Wrecsam | Llanfynydd STW | 4215 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 329498 | 352978 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5FW | LL115FW | ll11 5fw | ll115fw | Wrexham | Wrecsam | Llanfynydd STW | 4136 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 329492 | 353063 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5HA | LL115HA | ll11 5ha | ll115ha | Flintshire | Sir Y Fflint | Hope WwTW | 2090 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 329795 | 356149 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HB | LL115HB | ll11 5hb | ll115hb | Flintshire | Sir Y Fflint | Hope WwTW | 2249 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 329860 | 355957 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HD | LL115HD | ll11 5hd | ll115hd | Flintshire | Sir Y Fflint | Hope WwTW | 2433 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 330050 | 355715 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HF | LL115HF | ll11 5hf | ll115hf | Flintshire | Sir Y Fflint | Llanfynydd STW | 1228 | 960 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.89 | 9.54 | 10.55 | 328386 | 355791 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HG | LL115HG | ll11 5hg | ll115hg | Flintshire | Sir Y Fflint | Llanfynydd STW | 428 | 950 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.71 | 9.44 | 10.44 | 327995 | 356545 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HH | LL115HH | ll11 5hh | ll115hh | Flintshire | Sir Y Fflint | Llanfynydd STW | 170 | 950 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.71 | 9.44 | 10.44 | 327790 | 356755 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HJ | LL115HJ | ll11 5hj | ll115hj | Wrexham | Wrecsam | Llanfynydd STW | 4448 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329581 | 352759 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5HL | LL115HL | ll11 5hl | ll115hl | Flintshire | Sir Y Fflint | Llanfynydd STW | 924 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 328510 | 356503 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HN | LL115HN | ll11 5hn | ll115hn | Flintshire | Sir Y Fflint | Llanfynydd STW | 204 | 950 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.71 | 9.44 | 10.44 | 327729 | 356922 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HP | LL115HP | ll11 5hp | ll115hp | Flintshire | Sir Y Fflint | Llanfynydd STW | 1463 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 328041 | 358151 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HQ | LL115HQ | ll11 5hq | ll115hq | Wrexham | Wrecsam | Llanfynydd STW | 4371 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329596 | 352853 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5HR | LL115HR | ll11 5hr | ll115hr | Flintshire | Sir Y Fflint | Llanfynydd STW | 482 | 944 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.59 | 9.38 | 10.37 | 327154 | 356871 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HS | LL115HS | ll11 5hs | ll115hs | Flintshire | Sir Y Fflint | Llanfynydd STW | 1543 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 326122 | 356384 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HT | LL115HT | ll11 5ht | ll115ht | Flintshire | Sir Y Fflint | Treuddyn (Bridge Terrace) STW | 1993 | 985 | 900to1200 | 1.97 | 1.44 | 1.06 | 18.36 | 9.79 | 10.82 | 325115 | 355979 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HU | LL115HU | ll11 5hu | ll115hu | Flintshire | Sir Y Fflint | Llanfynydd STW | 1067 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 326707 | 356199 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HW | LL115HW | ll11 5hw | ll115hw | Flintshire | Sir Y Fflint | Llanfynydd STW | 936 | 934 | 900to1200 | 1.87 | 1.37 | 1 | 17.41 | 9.28 | 10.26 | 328167 | 357509 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5HX | LL115HX | ll11 5hx | ll115hx | Wrexham | Wrecsam | Llanfynydd STW | 4334 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329653 | 352924 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5HY | LL115HY | ll11 5hy | ll115hy | Flintshire | Sir Y Fflint | Llanfynydd STW | 1006 | 990 | 900to1200 | 1.98 | 1.45 | 1.06 | 18.45 | 9.84 | 10.88 | 327405 | 355768 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5LA | LL115LA | ll11 5la | ll115la | Flintshire | Sir Y Fflint | Llanfynydd STW | 796 | 960 | 900to1200 | 1.92 | 1.41 | 1.03 | 17.89 | 9.54 | 10.55 | 327992 | 356047 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5LB | LL115LB | ll11 5lb | ll115lb | Flintshire | Sir Y Fflint | Hope WwTW | 2114 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 329875 | 356094 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5LD | LL115LD | ll11 5ld | ll115ld | Wrexham | Wrecsam | Llanfynydd STW | 2978 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329773 | 354694 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5LE | LL115LE | ll11 5le | ll115le | Flintshire | Sir Y Fflint | Llanfynydd STW | 2019 | 933 | 900to1200 | 1.87 | 1.37 | 1 | 17.39 | 9.27 | 10.25 | 329314 | 355652 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5LF | LL115LF | ll11 5lf | ll115lf | Wrexham | Wrecsam | Llanfynydd STW | 2823 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329593 | 354732 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5LG | LL115LG | ll11 5lg | ll115lg | Flintshire | Sir Y Fflint | Llanfynydd STW | 1881 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 328555 | 355119 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5LH | LL115LH | ll11 5lh | ll115lh | Flintshire | Sir Y Fflint | Llanfynydd STW | 1688 | 965 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.99 | 9.59 | 10.6 | 328498 | 355309 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5LJ | LL115LJ | ll11 5lj | ll115lj | Flintshire | Sir Y Fflint | Llanfynydd STW | 1838 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 328614 | 355205 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5LL | LL115LL | ll11 5ll | ll115ll | Flintshire | Sir Y Fflint | Llanfynydd STW | 1766 | 965 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.99 | 9.59 | 10.6 | 328495 | 355217 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5LN | LL115LN | ll11 5ln | ll115ln | Flintshire | Sir Y Fflint | Llanfynydd STW | 1648 | 965 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.99 | 9.59 | 10.6 | 328480 | 355345 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5LP | LL115LP | ll11 5lp | ll115lp | Flintshire | Sir Y Fflint | Llanfynydd STW | 1592 | 965 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.99 | 9.59 | 10.6 | 328307 | 355315 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5LR | LL115LR | ll11 5lr | ll115lr | Wrexham | Wrecsam | Llanfynydd STW | 2494 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 328883 | 354600 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5LS | LL115LS | ll11 5ls | ll115ls | Wrexham | Wrecsam | Llanfynydd STW | 3174 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 328215 | 353633 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5LT | LL115LT | ll11 5lt | ll115lt | Wrexham | Wrecsam | Llanfynydd STW | 2327 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 328021 | 354459 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5LU | LL115LU | ll11 5lu | ll115lu | Wrexham | Wrecsam | Llanfynydd STW | 3775 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 328786 | 353161 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5LW | LL115LW | ll11 5lw | ll115lw | Flintshire | Sir Y Fflint | Llanfynydd STW | 1684 | 965 | 900to1200 | 1.93 | 1.41 | 1.04 | 17.99 | 9.59 | 10.6 | 328422 | 355270 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5LY | LL115LY | ll11 5ly | ll115ly | Wrexham | Wrecsam | Llanfynydd STW | 3376 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 328809 | 353591 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5NA | LL115NA | ll11 5na | ll115na | Wrexham | Wrecsam | Llanfynydd STW | 2843 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 328886 | 354206 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5NB | LL115NB | ll11 5nb | ll115nb | Wrexham | Wrecsam | Llanfynydd STW | 2956 | 931 | 900to1200 | 1.86 | 1.36 | 1 | 17.35 | 9.25 | 10.23 | 328748 | 354019 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5NF | LL115NF | ll11 5nf | ll115nf | Wrexham | Wrecsam | Llanfynydd STW | 5167 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330334 | 352355 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5NG | LL115NG | ll11 5ng | ll115ng | Wrexham | Wrecsam | Llanfynydd STW | 4682 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330129 | 352799 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5NP | LL115NP | ll11 5np | ll115np | Wrexham | Wrecsam | Llanfynydd STW | 4297 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330020 | 353188 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5NR | LL115NR | ll11 5nr | ll115nr | Wrexham | Wrecsam | Llanfynydd STW | 4858 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330087 | 352567 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5NS | LL115NS | ll11 5ns | ll115ns | Wrexham | Wrecsam | Llanfynydd STW | 5382 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330123 | 351987 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5NT | LL115NT | ll11 5nt | ll115nt | Wrexham | Wrecsam | Llanfynydd STW | 5476 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330138 | 351889 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5NW | LL115NW | ll11 5nw | ll115nw | Wrexham | Wrecsam | Llanfynydd STW | 4376 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330021 | 353093 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5NY | LL115NY | ll11 5ny | ll115ny | Wrexham | Wrecsam | Llanfynydd STW | 5599 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330160 | 351762 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PA | LL115PA | ll11 5pa | ll115pa | Wrexham | Wrecsam | Llanfynydd STW | 5609 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330179 | 351761 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PB | LL115PB | ll11 5pb | ll115pb | Wrexham | Wrecsam | Llanfynydd STW | 5556 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330169 | 351815 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PD | LL115PD | ll11 5pd | ll115pd | Wrexham | Wrecsam | Llanfynydd STW | 5551 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330193 | 351834 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PE | LL115PE | ll11 5pe | ll115pe | Wrexham | Wrecsam | Llanfynydd STW | 5528 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330138 | 351831 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PF | LL115PF | ll11 5pf | ll115pf | Wrexham | Wrecsam | Llanfynydd STW | 5549 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330226 | 351853 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PG | LL115PG | ll11 5pg | ll115pg | Wrexham | Wrecsam | Llanfynydd STW | 5638 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330224 | 351751 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PH | LL115PH | ll11 5ph | ll115ph | Wrexham | Wrecsam | Llanfynydd STW | 5892 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330515 | 351621 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PJ | LL115PJ | ll11 5pj | ll115pj | Wrexham | Wrecsam | Llanfynydd STW | 5630 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330168 | 351732 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PL | LL115PL | ll11 5pl | ll115pl | Wrexham | Wrecsam | Llanfynydd STW | 5839 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330459 | 351650 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PN | LL115PN | ll11 5pn | ll115pn | Wrexham | Wrecsam | Llanfynydd STW | 5848 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330470 | 351646 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PP | LL115PP | ll11 5pp | ll115pp | Wrexham | Wrecsam | Llanfynydd STW | 5851 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330503 | 351661 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PQ | LL115PQ | ll11 5pq | ll115pq | Wrexham | Wrecsam | Llanfynydd STW | 5657 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330181 | 351708 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PR | LL115PR | ll11 5pr | ll115pr | Wrexham | Wrecsam | Llanfynydd STW | 5829 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330482 | 351674 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PS | LL115PS | ll11 5ps | ll115ps | Wrexham | Wrecsam | Llanfynydd STW | 5802 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330441 | 351682 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PU | LL115PU | ll11 5pu | ll115pu | Wrexham | Wrecsam | Llanfynydd STW | 5824 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330498 | 351689 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PW | LL115PW | ll11 5pw | ll115pw | Wrexham | Wrecsam | Llanfynydd STW | 5860 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330510 | 351654 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5PY | LL115PY | ll11 5py | ll115py | Wrexham | Wrecsam | Llanfynydd STW | 5711 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330448 | 351791 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5RA | LL115RA | ll11 5ra | ll115ra | Wrexham | Wrecsam | Llanfynydd STW | 5750 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330467 | 351757 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5RB | LL115RB | ll11 5rb | ll115rb | Wrexham | Wrecsam | Llanfynydd STW | 5755 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330473 | 351754 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5RD | LL115RD | ll11 5rd | ll115rd | Wrexham | Wrecsam | Llanfynydd STW | 5909 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330568 | 351631 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5RE | LL115RE | ll11 5re | ll115re | Wrexham | Wrecsam | Llanfynydd STW | 5803 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330483 | 351705 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5RF | LL115RF | ll11 5rf | ll115rf | Wrexham | Wrecsam | Llanfynydd STW | 5779 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330466 | 351723 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5RG | LL115RG | ll11 5rg | ll115rg | Wrexham | Wrecsam | Llanfynydd STW | 5762 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330456 | 351737 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5RH | LL115RH | ll11 5rh | ll115rh | Wrexham | Wrecsam | Llanfynydd STW | 5750 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330451 | 351747 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5RN | LL115RN | ll11 5rn | ll115rn | Wrexham | Wrecsam | Llanfynydd STW | 5888 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330561 | 351651 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5RP | LL115RP | ll11 5rp | ll115rp | Wrexham | Wrecsam | Llanfynydd STW | 5805 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330505 | 351715 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5RR | LL115RR | ll11 5rr | ll115rr | Wrexham | Wrecsam | Llanfynydd STW | 5679 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330466 | 351838 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5RS | LL115RS | ll11 5rs | ll115rs | Wrexham | Wrecsam | Llanfynydd STW | 5751 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330399 | 351717 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5RW | LL115RW | ll11 5rw | ll115rw | Wrexham | Wrecsam | Llanfynydd STW | 5839 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330527 | 351688 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SA | LL115SA | ll11 5sa | ll115sa | Wrexham | Wrecsam | Llanfynydd STW | 5082 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329743 | 352135 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SB | LL115SB | ll11 5sb | ll115sb | Wrexham | Wrecsam | Llanfynydd STW | 4998 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329672 | 352194 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SD | LL115SD | ll11 5sd | ll115sd | Wrexham | Wrecsam | Llanfynydd STW | 4940 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329493 | 352181 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SE | LL115SE | ll11 5se | ll115se | Wrexham | Wrecsam | Llanfynydd STW | 4979 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329534 | 352155 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SF | LL115SF | ll11 5sf | ll115sf | Wrexham | Wrecsam | Llanfynydd STW | 5015 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329511 | 352107 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SG | LL115SG | ll11 5sg | ll115sg | Wrexham | Wrecsam | Llanfynydd STW | 4958 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329612 | 352212 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SH | LL115SH | ll11 5sh | ll115sh | Wrexham | Wrecsam | Llanfynydd STW | 4890 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329623 | 352291 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SJ | LL115SJ | ll11 5sj | ll115sj | Wrexham | Wrecsam | Llanfynydd STW | 5000 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329644 | 352180 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SL | LL115SL | ll11 5sl | ll115sl | Wrexham | Wrecsam | Llanfynydd STW | 4893 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329654 | 352302 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SN | LL115SN | ll11 5sn | ll115sn | Wrexham | Wrecsam | Llanfynydd STW | 4871 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329658 | 352328 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SQ | LL115SQ | ll11 5sq | ll115sq | Wrexham | Wrecsam | Llanfynydd STW | 4860 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329681 | 352350 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SR | LL115SR | ll11 5sr | ll115sr | Wrexham | Wrecsam | Llanfynydd STW | 4771 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329462 | 352351 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SS | LL115SS | ll11 5ss | ll115ss | Wrexham | Wrecsam | Llanfynydd STW | 4814 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329442 | 352296 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5ST | LL115ST | ll11 5st | ll115st | Wrexham | Wrecsam | Llanfynydd STW | 4883 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329521 | 352254 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SU | LL115SU | ll11 5su | ll115su | Wrexham | Wrecsam | Llanfynydd STW | 4895 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329544 | 352251 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SW | LL115SW | ll11 5sw | ll115sw | Wrexham | Wrecsam | Llanfynydd STW | 4792 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329561 | 352371 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SX | LL115SX | ll11 5sx | ll115sx | Wrexham | Wrecsam | Llanfynydd STW | 4998 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329485 | 352115 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SY | LL115SY | ll11 5sy | ll115sy | Wrexham | Wrecsam | Llanfynydd STW | 4998 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329729 | 352221 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5SZ | LL115SZ | ll11 5sz | ll115sz | Wrexham | Wrecsam | Llanfynydd STW | 5320 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329882 | 351937 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TA | LL115TA | ll11 5ta | ll115ta | Wrexham | Wrecsam | Llanfynydd STW | 4974 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329755 | 352259 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TB | LL115TB | ll11 5tb | ll115tb | Wrexham | Wrecsam | Llanfynydd STW | 4976 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329694 | 352229 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TD | LL115TD | ll11 5td | ll115td | Wrexham | Wrecsam | Llanfynydd STW | 4987 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329709 | 352224 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TE | LL115TE | ll11 5te | ll115te | Wrexham | Wrecsam | Llanfynydd STW | 5008 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329756 | 352222 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TF | LL115TF | ll11 5tf | ll115tf | Wrexham | Wrecsam | Llanfynydd STW | 4948 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329776 | 352298 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TG | LL115TG | ll11 5tg | ll115tg | Wrexham | Wrecsam | Llanfynydd STW | 4929 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 329916 | 352390 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TH | LL115TH | ll11 5th | ll115th | Wrexham | Wrecsam | Llanfynydd STW | 4670 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329369 | 352422 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TJ | LL115TJ | ll11 5tj | ll115tj | Wrexham | Wrecsam | Llanfynydd STW | 4730 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329498 | 352411 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TL | LL115TL | ll11 5tl | ll115tl | Wrexham | Wrecsam | Llanfynydd STW | 4690 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329162 | 352322 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TN | LL115TN | ll11 5tn | ll115tn | Wrexham | Wrecsam | Llanfynydd STW | 4781 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329233 | 352251 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TP | LL115TP | ll11 5tp | ll115tp | Wrexham | Wrecsam | Llanfynydd STW | 4698 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329429 | 352416 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TQ | LL115TQ | ll11 5tq | ll115tq | Wrexham | Wrecsam | Llanfynydd STW | 4656 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329441 | 352467 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TR | LL115TR | ll11 5tr | ll115tr | Wrexham | Wrecsam | Llanfynydd STW | 4689 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 326149 | 352299 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TS | LL115TS | ll11 5ts | ll115ts | Wrexham | Wrecsam | Llanfynydd STW | 4733 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 325779 | 352391 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TT | LL115TT | ll11 5tt | ll115tt | Wrexham | Wrecsam | Llanfynydd STW | 4754 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 325632 | 352433 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TU | LL115TU | ll11 5tu | ll115tu | Wrexham | Wrecsam | Llanfynydd STW | 4860 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329194 | 352154 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TW | LL115TW | ll11 5tw | ll115tw | Wrexham | Wrecsam | Llanfynydd STW | 5027 | 942 | 900to1200 | 1.89 | 1.38 | 1.01 | 17.56 | 9.36 | 10.35 | 329209 | 351982 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5TY | LL115TY | ll11 5ty | ll115ty | Wrexham | Wrecsam | Llanfynydd STW | 3496 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 327735 | 353257 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UA | LL115UA | ll11 5ua | ll115ua | Wrexham | Wrecsam | Llanfynydd STW | 3482 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 326938 | 353337 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UB | LL115UB | ll11 5ub | ll115ub | Wrexham | Wrecsam | Llanfynydd STW | 3524 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 326661 | 353360 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UD | LL115UD | ll11 5ud | ll115ud | Wrexham | Wrecsam | Llanfynydd STW | 3490 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 326758 | 353369 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UE | LL115UE | ll11 5ue | ll115ue | Wrexham | Wrecsam | Llanfynydd STW | 3760 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 326661 | 353116 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UF | LL115UF | ll11 5uf | ll115uf | Wrexham | Wrecsam | Llanfynydd STW | 4202 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 326397 | 352731 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UG | LL115UG | ll11 5ug | ll115ug | Wrexham | Wrecsam | Llanfynydd STW | 4192 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 326061 | 352860 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UH | LL115UH | ll11 5uh | ll115uh | Wrexham | Wrecsam | Llanfynydd STW | 4366 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 325517 | 352925 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UJ | LL115UJ | ll11 5uj | ll115uj | Wrexham | Wrecsam | Llanfynydd STW | 3487 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 326579 | 353423 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UL | LL115UL | ll11 5ul | ll115ul | Wrexham | Wrecsam | Grainnrhyd STW | 4710 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 324646 | 352549 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UN | LL115UN | ll11 5un | ll115un | Wrexham | Wrecsam | Llanfynydd STW | 4389 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 325947 | 352694 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UP | LL115UP | ll11 5up | ll115up | Wrexham | Wrecsam | Llanfynydd STW | 4572 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 325918 | 352508 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UQ | LL115UQ | ll11 5uq | ll115uq | Wrexham | Wrecsam | Llanfynydd STW | 4594 | 948 | 900to1200 | 1.9 | 1.39 | 1.02 | 17.67 | 9.42 | 10.42 | 329456 | 352541 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UR | LL115UR | ll11 5ur | ll115ur | Wrexham | Wrecsam | Llanfynydd STW | 3692 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 326579 | 353209 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5US | LL115US | ll11 5us | ll115us | Wrexham | Wrecsam | Llanfynydd STW | 3675 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 326549 | 353236 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UT | LL115UT | ll11 5ut | ll115ut | Wrexham | Wrecsam | Llanfynydd STW | 3559 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 326377 | 353416 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UU | LL115UU | ll11 5uu | ll115uu | Wrexham | Wrecsam | Llanfynydd STW | 4005 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 325673 | 353252 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UW | LL115UW | ll11 5uw | ll115uw | Wrexham | Wrecsam | Llanfynydd STW | 4441 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 326099 | 352579 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UX | LL115UX | ll11 5ux | ll115ux | Wrexham | Wrecsam | Llanfynydd STW | 3454 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 326898 | 353373 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5UY | LL115UY | ll11 5uy | ll115uy | Wrexham | Wrecsam | Llanfynydd STW | 3648 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 326209 | 353387 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YA | LL115YA | ll11 5ya | ll115ya | Wrexham | Wrecsam | Llanfynydd STW | 3515 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 326253 | 353513 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YB | LL115YB | ll11 5yb | ll115yb | Wrexham | Wrecsam | Llanfynydd STW | 3633 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 326317 | 353360 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YD | LL115YD | ll11 5yd | ll115yd | Wrexham | Wrecsam | Llanfynydd STW | 2722 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 327248 | 354054 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YE | LL115YE | ll11 5ye | ll115ye | Wrexham | Wrecsam | Llanfynydd STW | 3370 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 326816 | 353478 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YF | LL115YF | ll11 5yf | ll115yf | Wrexham | Wrecsam | Llanfynydd STW | 3253 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 326954 | 353567 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YG | LL115YG | ll11 5yg | ll115yg | Wrexham | Wrecsam | Llanfynydd STW | 2935 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 326887 | 353909 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YH | LL115YH | ll11 5yh | ll115yh | Wrexham | Wrecsam | Llanfynydd STW | 3739 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 326328 | 353243 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YJ | LL115YJ | ll11 5yj | ll115yj | Wrexham | Wrecsam | Llanfynydd STW | 3427 | 1033 | 900to1200 | 2.07 | 1.51 | 1.11 | 19.25 | 10.27 | 11.35 | 326855 | 353411 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YL | LL115YL | ll11 5yl | ll115yl | Wrexham | Wrecsam | Grainnrhyd STW | 4369 | 1068 | 900to1200 | 2.14 | 1.56 | 1.15 | 19.91 | 10.62 | 11.73 | 324744 | 353124 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YN | LL115YN | ll11 5yn | ll115yn | Wrexham | Wrecsam | Llanfynydd STW | 3693 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 325866 | 353501 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YP | LL115YP | ll11 5yp | ll115yp | Flintshire | Sir Y Fflint | Grainnrhyd STW | 4004 | 1042 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.42 | 10.36 | 11.45 | 324599 | 353512 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5YQ | LL115YQ | ll11 5yq | ll115yq | Wrexham | Wrecsam | Llanfynydd STW | 3479 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 326308 | 353529 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YR | LL115YR | ll11 5yr | ll115yr | Flintshire | Sir Y Fflint | Llanfynydd STW | 3212 | 1036 | 900to1200 | 2.07 | 1.52 | 1.11 | 19.31 | 10.3 | 11.38 | 325500 | 354339 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5YS | LL115YS | ll11 5ys | ll115ys | Wrexham | Wrecsam | Llanfynydd STW | 3534 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 326389 | 353439 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YT | LL115YT | ll11 5yt | ll115yt | Wrexham | Wrecsam | Llanfynydd STW | 3702 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 326476 | 353230 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YU | LL115YU | ll11 5yu | ll115yu | Wrexham | Wrecsam | Llanfynydd STW | 4721 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 325674 | 352451 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YW | LL115YW | ll11 5yw | ll115yw | Flintshire | Sir Y Fflint | Llanfynydd STW | 4143 | 1042 | 900to1200 | 2.09 | 1.53 | 1.12 | 19.42 | 10.36 | 11.45 | 324942 | 353591 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL11 5YX | LL115YX | ll11 5yx | ll115yx | Wrexham | Wrecsam | Llanfynydd STW | 3696 | 1049 | 900to1200 | 2.1 | 1.54 | 1.13 | 19.55 | 10.43 | 11.53 | 326395 | 353264 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YY | LL115YY | ll11 5yy | ll115yy | Wrexham | Wrecsam | Llanfynydd STW | 4702 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 325835 | 352402 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 5YZ | LL115YZ | ll11 5yz | ll115yz | Wrexham | Wrecsam | Llanfynydd STW | 4672 | 1065 | 900to1200 | 2.13 | 1.56 | 1.14 | 19.85 | 10.59 | 11.7 | 325731 | 352479 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AA | LL116AA | ll11 6aa | ll116aa | Wrexham | Wrecsam | Llanfynydd STW | 5017 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330748 | 352830 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AB | LL116AB | ll11 6ab | ll116ab | Wrexham | Wrecsam | Llanfynydd STW | 4898 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330609 | 352872 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AD | LL116AD | ll11 6ad | ll116ad | Wrexham | Wrecsam | Llanfynydd STW | 5053 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330698 | 352745 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AE | LL116AE | ll11 6ae | ll116ae | Wrexham | Wrecsam | Llanfynydd STW | 5094 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330748 | 352732 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AF | LL116AF | ll11 6af | ll116af | Wrexham | Wrecsam | Llanfynydd STW | 4891 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330580 | 352859 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AG | LL116AG | ll11 6ag | ll116ag | Wrexham | Wrecsam | Llanfynydd STW | 4621 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330505 | 353142 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AH | LL116AH | ll11 6ah | ll116ah | Wrexham | Wrecsam | Llanfynydd STW | 4610 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330481 | 353137 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AJ | LL116AJ | ll11 6aj | ll116aj | Wrexham | Wrecsam | Llanfynydd STW | 4398 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330383 | 353330 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AL | LL116AL | ll11 6al | ll116al | Wrexham | Wrecsam | Llanfynydd STW | 4775 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330605 | 353025 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AN | LL116AN | ll11 6an | ll116an | Wrexham | Wrecsam | Llanfynydd STW | 4138 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330158 | 353484 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AP | LL116AP | ll11 6ap | ll116ap | Wrexham | Wrecsam | Llanfynydd STW | 4705 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330603 | 353113 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AQ | LL116AQ | ll11 6aq | ll116aq | Wrexham | Wrecsam | Llanfynydd STW | 5205 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330650 | 352520 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AR | LL116AR | ll11 6ar | ll116ar | Wrexham | Wrecsam | Llanfynydd STW | 4683 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330483 | 353046 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AT | LL116AT | ll11 6at | ll116at | Wrexham | Wrecsam | Llanfynydd STW | 4500 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330494 | 353289 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AU | LL116AU | ll11 6au | ll116au | Wrexham | Wrecsam | Llanfynydd STW | 4416 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330477 | 353385 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AW | LL116AW | ll11 6aw | ll116aw | Wrexham | Wrecsam | Llanfynydd STW | 4439 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330420 | 353307 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AX | LL116AX | ll11 6ax | ll116ax | Wrexham | Wrecsam | Llanfynydd STW | 4676 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330543 | 353102 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AY | LL116AY | ll11 6ay | ll116ay | Wrexham | Wrecsam | Llanfynydd STW | 5084 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330719 | 352722 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6AZ | LL116AZ | ll11 6az | ll116az | Wrexham | Wrecsam | Llanfynydd STW | 4756 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330623 | 353064 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BA | LL116BA | ll11 6ba | ll116ba | Wrexham | Wrecsam | Llanfynydd STW | 4281 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330423 | 353516 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BB | LL116BB | ll11 6bb | ll116bb | Wrexham | Wrecsam | Llanfynydd STW | 4262 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330337 | 353468 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BD | LL116BD | ll11 6bd | ll116bd | Wrexham | Wrecsam | Llanfynydd STW | 4068 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330369 | 353753 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BE | LL116BE | ll11 6be | ll116be | Wrexham | Wrecsam | Llanfynydd STW | 3979 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330040 | 353593 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BF | LL116BF | ll11 6bf | ll116bf | Wrexham | Wrecsam | Llanfynydd STW | 4202 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330676 | 353868 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BG | LL116BG | ll11 6bg | ll116bg | Wrexham | Wrecsam | Llanfynydd STW | 3992 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330026 | 353566 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BH | LL116BH | ll11 6bh | ll116bh | Wrexham | Wrecsam | Llanfynydd STW | 3567 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329848 | 353966 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BJ | LL116BJ | ll11 6bj | ll116bj | Wrexham | Wrecsam | Llanfynydd STW | 3852 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329941 | 353678 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BL | LL116BL | ll11 6bl | ll116bl | Wrexham | Wrecsam | Llanfynydd STW | 3872 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329983 | 353684 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BN | LL116BN | ll11 6bn | ll116bn | Wrexham | Wrecsam | Llanfynydd STW | 3654 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329856 | 353862 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BP | LL116BP | ll11 6bp | ll116bp | Wrexham | Wrecsam | Llanfynydd STW | 3914 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330035 | 353672 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BQ | LL116BQ | ll11 6bq | ll116bq | Wrexham | Wrecsam | Llanfynydd STW | 4184 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330274 | 353517 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BS | LL116BS | ll11 6bs | ll116bs | Wrexham | Wrecsam | Llanfynydd STW | 3664 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329886 | 353872 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BT | LL116BT | ll11 6bt | ll116bt | Wrexham | Wrecsam | Llanfynydd STW | 4289 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330204 | 353328 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BU | LL116BU | ll11 6bu | ll116bu | Wrexham | Wrecsam | Llanfynydd STW | 3451 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 329870 | 354135 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BW | LL116BW | ll11 6bw | ll116bw | Wrexham | Wrecsam | Llanfynydd STW | 3676 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330075 | 354016 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BX | LL116BX | ll11 6bx | ll116bx | Wrexham | Wrecsam | Llanfynydd STW | 4127 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330267 | 353586 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BY | LL116BY | ll11 6by | ll116by | Wrexham | Wrecsam | Llanfynydd STW | 4394 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330438 | 353380 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6BZ | LL116BZ | ll11 6bz | ll116bz | Wrexham | Wrecsam | Gresford STW | 5331 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331372 | 351768 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DA | LL116DA | ll11 6da | ll116da | Wrexham | Wrecsam | Llanfynydd STW | 4921 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330680 | 352898 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DB | LL116DB | ll11 6db | ll116db | Wrexham | Wrecsam | Llanfynydd STW | 4848 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330715 | 353021 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DD | LL116DD | ll11 6dd | ll116dd | Wrexham | Wrecsam | Llanfynydd STW | 4821 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330693 | 353037 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DE | LL116DE | ll11 6de | ll116de | Wrexham | Wrecsam | Llanfynydd STW | 4778 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330651 | 353058 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DF | LL116DF | ll11 6df | ll116df | Wrexham | Wrecsam | Llanfynydd STW | 4282 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330467 | 353553 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DG | LL116DG | ll11 6dg | ll116dg | Wrexham | Wrecsam | Gresford STW | 4992 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330863 | 352819 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DH | LL116DH | ll11 6dh | ll116dh | Wrexham | Wrecsam | Llanfynydd STW | 4792 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330789 | 353157 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DJ | LL116DJ | ll11 6dj | ll116dj | Wrexham | Wrecsam | Llanfynydd STW | 4721 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330664 | 353144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DL | LL116DL | ll11 6dl | ll116dl | Wrexham | Wrecsam | Gresford STW | 4901 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330875 | 352958 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DN | LL116DN | ll11 6dn | ll116dn | Wrexham | Wrecsam | Llanfynydd STW | 4395 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330722 | 353639 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DP | LL116DP | ll11 6dp | ll116dp | Wrexham | Wrecsam | Gresford STW | 5449 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331389 | 351599 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DQ | LL116DQ | ll11 6dq | ll116dq | Wrexham | Wrecsam | Llanfynydd STW | 4671 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330669 | 353214 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DR | LL116DR | ll11 6dr | ll116dr | Wrexham | Wrecsam | Llanfynydd STW | 4411 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330612 | 353511 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DS | LL116DS | ll11 6ds | ll116ds | Wrexham | Wrecsam | Llanfynydd STW | 4376 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330532 | 353485 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DT | LL116DT | ll11 6dt | ll116dt | Wrexham | Wrecsam | Llanfynydd STW | 4370 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330531 | 353493 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DU | LL116DU | ll11 6du | ll116du | Wrexham | Wrecsam | Llanfynydd STW | 4343 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330561 | 353557 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DW | LL116DW | ll11 6dw | ll116dw | Wrexham | Wrecsam | Llanfynydd STW | 4475 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330637 | 353447 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DX | LL116DX | ll11 6dx | ll116dx | Wrexham | Wrecsam | Gresford STW | 5423 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331371 | 351648 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DY | LL116DY | ll11 6dy | ll116dy | Wrexham | Wrecsam | Llanfynydd STW | 4229 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330487 | 353643 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6DZ | LL116DZ | ll11 6dz | ll116dz | Wrexham | Wrecsam | Gresford STW | 5422 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331321 | 351692 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EA | LL116EA | ll11 6ea | ll116ea | Wrexham | Wrecsam | Llanfynydd STW | 4280 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330570 | 353651 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EB | LL116EB | ll11 6eb | ll116eb | Wrexham | Wrecsam | Llanfynydd STW | 4182 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330430 | 353655 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6ED | LL116ED | ll11 6ed | ll116ed | Wrexham | Wrecsam | Llanfynydd STW | 4173 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330446 | 353682 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EE | LL116EE | ll11 6ee | ll116ee | Wrexham | Wrecsam | Llanfynydd STW | 4251 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330581 | 353702 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EF | LL116EF | ll11 6ef | ll116ef | Wrexham | Wrecsam | Llanfynydd STW | 4184 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330483 | 353701 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EG | LL116EG | ll11 6eg | ll116eg | Wrexham | Wrecsam | Llanfynydd STW | 4194 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330543 | 353744 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EH | LL116EH | ll11 6eh | ll116eh | Wrexham | Wrecsam | Llanfynydd STW | 4180 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330555 | 353776 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EJ | LL116EJ | ll11 6ej | ll116ej | Wrexham | Wrecsam | Llanfynydd STW | 4104 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330421 | 353752 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EL | LL116EL | ll11 6el | ll116el | Wrexham | Wrecsam | Llanfynydd STW | 4089 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330478 | 353828 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EN | LL116EN | ll11 6en | ll116en | Wrexham | Wrecsam | Llanfynydd STW | 4163 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330486 | 353732 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EP | LL116EP | ll11 6ep | ll116ep | Wrexham | Wrecsam | Llanfynydd STW | 4021 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330468 | 353914 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EQ | LL116EQ | ll11 6eq | ll116eq | Wrexham | Wrecsam | Gresford STW | 5348 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331455 | 351675 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6ER | LL116ER | ll11 6er | ll116er | Wrexham | Wrecsam | Gresford STW | 5423 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331479 | 351558 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6ES | LL116ES | ll11 6es | ll116es | Wrexham | Wrecsam | Llanfynydd STW | 4273 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330678 | 353768 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6ET | LL116ET | ll11 6et | ll116et | Wrexham | Wrecsam | Llanfynydd STW | 4379 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330686 | 353626 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EU | LL116EU | ll11 6eu | ll116eu | Wrexham | Wrecsam | Llanfynydd STW | 4156 | 881 | 700to900 | 1.76 | 1.29 | 0.95 | 16.42 | 8.76 | 9.68 | 330648 | 353906 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EW | LL116EW | ll11 6ew | ll116ew | Wrexham | Wrecsam | Llanfynydd STW | 4036 | 903 | 900to1200 | 1.81 | 1.32 | 0.97 | 16.83 | 8.98 | 9.92 | 330435 | 353860 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EX | LL116EX | ll11 6ex | ll116ex | Wrexham | Wrecsam | Gresford STW | 5310 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331409 | 351764 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6EZ | LL116EZ | ll11 6ez | ll116ez | Wrexham | Wrecsam | Llanfynydd STW | 4352 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330406 | 353409 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6FA | LL116FA | ll11 6fa | ll116fa | Wrexham | Wrecsam | Gresford STW | 5377 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331219 | 351844 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6FB | LL116FB | ll11 6fb | ll116fb | Wrexham | Wrecsam | Gresford STW | 5407 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331247 | 351778 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6FD | LL116FD | ll11 6fd | ll116fd | Wrexham | Wrecsam | Gresford STW | 5314 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331268 | 351885 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HA | LL116HA | ll11 6ha | ll116ha | Wrexham | Wrecsam | Gresford STW | 4699 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330971 | 353175 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HB | LL116HB | ll11 6hb | ll116hb | Wrexham | Wrecsam | Gresford STW | 4674 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 331041 | 353116 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HD | LL116HD | ll11 6hd | ll116hd | Wrexham | Wrecsam | Llanfynydd STW | 4900 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330703 | 352944 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HF | LL116HF | ll11 6hf | ll116hf | Wrexham | Wrecsam | Llanfynydd STW | 5022 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330786 | 352854 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HG | LL116HG | ll11 6hg | ll116hg | Wrexham | Wrecsam | Gresford STW | 5029 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330832 | 352799 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HH | LL116HH | ll11 6hh | ll116hh | Wrexham | Wrecsam | Gresford STW | 5061 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330802 | 352785 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HJ | LL116HJ | ll11 6hj | ll116hj | Wrexham | Wrecsam | Gresford STW | 5087 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331009 | 352483 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HL | LL116HL | ll11 6hl | ll116hl | Wrexham | Wrecsam | Llanfynydd STW | 5057 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330773 | 352798 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HN | LL116HN | ll11 6hn | ll116hn | Wrexham | Wrecsam | Llanfynydd STW | 5065 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330781 | 352794 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HP | LL116HP | ll11 6hp | ll116hp | Wrexham | Wrecsam | Gresford STW | 5064 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330919 | 352628 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HR | LL116HR | ll11 6hr | ll116hr | Wrexham | Wrecsam | Gresford STW | 5115 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330945 | 352515 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HS | LL116HS | ll11 6hs | ll116hs | Wrexham | Wrecsam | Gresford STW | 5167 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330998 | 352373 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HT | LL116HT | ll11 6ht | ll116ht | Wrexham | Wrecsam | Gresford STW | 5139 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331059 | 352346 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HU | LL116HU | ll11 6hu | ll116hu | Wrexham | Wrecsam | Gresford STW | 5190 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331077 | 352251 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HW | LL116HW | ll11 6hw | ll116hw | Wrexham | Wrecsam | Gresford STW | 5082 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330788 | 352769 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HX | LL116HX | ll11 6hx | ll116hx | Wrexham | Wrecsam | Gresford STW | 5610 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330947 | 351782 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HY | LL116HY | ll11 6hy | ll116hy | Wrexham | Wrecsam | Gresford STW | 5201 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331079 | 352232 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6HZ | LL116HZ | ll11 6hz | ll116hz | Wrexham | Wrecsam | Gresford STW | 5211 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331108 | 352187 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6JA | LL116JA | ll11 6ja | ll116ja | Wrexham | Wrecsam | Gresford STW | 5410 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331083 | 351929 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6JB | LL116JB | ll11 6jb | ll116jb | Wrexham | Wrecsam | Gresford STW | 5349 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331084 | 352014 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6JD | LL116JD | ll11 6jd | ll116jd | Wrexham | Wrecsam | Gresford STW | 5377 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331090 | 351968 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6JE | LL116JE | ll11 6je | ll116je | Wrexham | Wrecsam | Gresford STW | 5447 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331043 | 351917 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6JF | LL116JF | ll11 6jf | ll116jf | Wrexham | Wrecsam | Gresford STW | 5545 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331010 | 351812 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6JG | LL116JG | ll11 6jg | ll116jg | Wrexham | Wrecsam | Gresford STW | 5511 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331024 | 351846 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LA | LL116LA | ll11 6la | ll116la | Wrexham | Wrecsam | Gresford STW | 5208 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331053 | 352250 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LB | LL116LB | ll11 6lb | ll116lb | Wrexham | Wrecsam | Gresford STW | 5189 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330998 | 352339 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LD | LL116LD | ll11 6ld | ll116ld | Wrexham | Wrecsam | Gresford STW | 5187 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331040 | 352295 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LE | LL116LE | ll11 6le | ll116le | Wrexham | Wrecsam | Gresford STW | 5221 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331005 | 352284 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LF | LL116LF | ll11 6lf | ll116lf | Wrexham | Wrecsam | Gresford STW | 5239 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331048 | 352210 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LG | LL116LG | ll11 6lg | ll116lg | Wrexham | Wrecsam | Gresford STW | 5158 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330964 | 352425 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LH | LL116LH | ll11 6lh | ll116lh | Wrexham | Wrecsam | Gresford STW | 5199 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330942 | 352389 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LJ | LL116LJ | ll11 6lj | ll116lj | Wrexham | Wrecsam | Gresford STW | 5311 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331001 | 352155 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LL | LL116LL | ll11 6ll | ll116ll | Wrexham | Wrecsam | Gresford STW | 5382 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330909 | 352150 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LN | LL116LN | ll11 6ln | ll116ln | Wrexham | Wrecsam | Gresford STW | 5300 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330925 | 352255 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LQ | LL116LQ | ll11 6lq | ll116lq | Wrexham | Wrecsam | Gresford STW | 5289 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330977 | 352214 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LR | LL116LR | ll11 6lr | ll116lr | Wrexham | Wrecsam | Llanfynydd STW | 5324 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330554 | 352309 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LS | LL116LS | ll11 6ls | ll116ls | Wrexham | Wrecsam | Llanfynydd STW | 5345 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330648 | 352348 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LT | LL116LT | ll11 6lt | ll116lt | Wrexham | Wrecsam | Llanfynydd STW | 5442 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330615 | 352208 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LU | LL116LU | ll11 6lu | ll116lu | Wrexham | Wrecsam | Llanfynydd STW | 5343 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330691 | 352380 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LW | LL116LW | ll11 6lw | ll116lw | Wrexham | Wrecsam | Llanfynydd STW | 5494 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330689 | 352195 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LY | LL116LY | ll11 6ly | ll116ly | Wrexham | Wrecsam | Gresford STW | 5414 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330727 | 352309 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6LZ | LL116LZ | ll11 6lz | ll116lz | Wrexham | Wrecsam | Gresford STW | 5385 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330981 | 352068 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NA | LL116NA | ll11 6na | ll116na | Wrexham | Wrecsam | Llanfynydd STW | 5300 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330618 | 352382 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NB | LL116NB | ll11 6nb | ll116nb | Wrexham | Wrecsam | Llanfynydd STW | 5249 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330558 | 352403 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6ND | LL116ND | ll11 6nd | ll116nd | Wrexham | Wrecsam | Gresford STW | 5114 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330833 | 352656 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NE | LL116NE | ll11 6ne | ll116ne | Wrexham | Wrecsam | Gresford STW | 5304 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330827 | 352362 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NF | LL116NF | ll11 6nf | ll116nf | Wrexham | Wrecsam | Gresford STW | 5215 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330832 | 352495 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NG | LL116NG | ll11 6ng | ll116ng | Wrexham | Wrecsam | Gresford STW | 5197 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330816 | 352544 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NH | LL116NH | ll11 6nh | ll116nh | Wrexham | Wrecsam | Gresford STW | 5271 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330818 | 352424 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NJ | LL116NJ | ll11 6nj | ll116nj | Wrexham | Wrecsam | Gresford STW | 5326 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330851 | 352300 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NL | LL116NL | ll11 6nl | ll116nl | Wrexham | Wrecsam | Gresford STW | 5328 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330785 | 352374 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NN | LL116NN | ll11 6nn | ll116nn | Wrexham | Wrecsam | Gresford STW | 5155 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330868 | 352546 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NP | LL116NP | ll11 6np | ll116np | Wrexham | Wrecsam | Gresford STW | 5164 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330868 | 352531 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NQ | LL116NQ | ll11 6nq | ll116nq | Wrexham | Wrecsam | Gresford STW | 5113 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330853 | 352632 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NR | LL116NR | ll11 6nr | ll116nr | Wrexham | Wrecsam | Gresford STW | 5207 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330885 | 352443 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NS | LL116NS | ll11 6ns | ll116ns | Wrexham | Wrecsam | Gresford STW | 5240 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330891 | 352385 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NT | LL116NT | ll11 6nt | ll116nt | Wrexham | Wrecsam | Gresford STW | 5232 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330838 | 352461 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NU | LL116NU | ll11 6nu | ll116nu | Wrexham | Wrecsam | Gresford STW | 5197 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330877 | 352468 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NW | LL116NW | ll11 6nw | ll116nw | Wrexham | Wrecsam | Gresford STW | 5115 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330882 | 352592 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6NY | LL116NY | ll11 6ny | ll116ny | Wrexham | Wrecsam | Gresford STW | 5163 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330903 | 352491 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PA | LL116PA | ll11 6pa | ll116pa | Wrexham | Wrecsam | Gresford STW | 5205 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330761 | 352601 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PB | LL116PB | ll11 6pb | ll116pb | Wrexham | Wrecsam | Gresford STW | 5227 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330779 | 352542 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PD | LL116PD | ll11 6pd | ll116pd | Wrexham | Wrecsam | Gresford STW | 5145 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330795 | 352655 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PE | LL116PE | ll11 6pe | ll116pe | Wrexham | Wrecsam | Llanfynydd STW | 5174 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330725 | 352614 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PF | LL116PF | ll11 6pf | ll116pf | Wrexham | Wrecsam | Llanfynydd STW | 5257 | 872 | 700to900 | 1.75 | 1.28 | 0.94 | 16.25 | 8.67 | 9.58 | 330742 | 352523 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PJ | LL116PJ | ll11 6pj | ll116pj | Wrexham | Wrecsam | Llanfynydd STW | 5882 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330578 | 351668 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PL | LL116PL | ll11 6pl | ll116pl | Wrexham | Wrecsam | Llanfynydd STW | 6277 | 899 | 700to900 | 1.8 | 1.32 | 0.97 | 16.76 | 8.94 | 9.88 | 330488 | 351169 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PN | LL116PN | ll11 6pn | ll116pn | Wrexham | Wrecsam | Llanfynydd STW | 5804 | 891 | 700to900 | 1.78 | 1.3 | 0.96 | 16.61 | 8.86 | 9.79 | 330114 | 351511 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PP | LL116PP | ll11 6pp | ll116pp | Wrexham | Wrecsam | Llanfynydd STW | 6005 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330609 | 351544 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PR | LL116PR | ll11 6pr | ll116pr | Wrexham | Wrecsam | Gresford STW | 5987 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330653 | 351543 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PS | LL116PS | ll11 6ps | ll116ps | Wrexham | Wrecsam | Gresford STW | 5926 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330652 | 351631 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PT | LL116PT | ll11 6pt | ll116pt | Wrexham | Wrecsam | Gresford STW | 5817 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330699 | 351739 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PU | LL116PU | ll11 6pu | ll116pu | Wrexham | Wrecsam | Llanfynydd STW | 5827 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330625 | 351760 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PW | LL116PW | ll11 6pw | ll116pw | Wrexham | Wrecsam | Llanfynydd STW | 6310 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 330504 | 351140 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6PY | LL116PY | ll11 6py | ll116py | Wrexham | Wrecsam | Llanfynydd STW | 5757 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330643 | 351853 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6QA | LL116QA | ll11 6qa | ll116qa | Wrexham | Wrecsam | Gresford STW | 5766 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330934 | 351579 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6QD | LL116QD | ll11 6qd | ll116qd | Wrexham | Wrecsam | Gresford STW | 5878 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 330871 | 351484 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6QF | LL116QF | ll11 6qf | ll116qf | Wrexham | Wrecsam | Gresford STW | 5879 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330783 | 351566 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6QG | LL116QG | ll11 6qg | ll116qg | Wrexham | Wrecsam | Gresford STW | 5808 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330914 | 351540 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RA | LL116RA | ll11 6ra | ll116ra | Wrexham | Wrecsam | Llanfynydd STW | 5757 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330600 | 351826 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RB | LL116RB | ll11 6rb | ll116rb | Wrexham | Wrecsam | Gresford STW | 5713 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330683 | 351907 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RD | LL116RD | ll11 6rd | ll116rd | Wrexham | Wrecsam | Llanfynydd STW | 5660 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330647 | 351970 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RE | LL116RE | ll11 6re | ll116re | Wrexham | Wrecsam | Llanfynydd STW | 5707 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330657 | 351920 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RF | LL116RF | ll11 6rf | ll116rf | Wrexham | Wrecsam | Llanfynydd STW | 5617 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330600 | 351991 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RG | LL116RG | ll11 6rg | ll116rg | Wrexham | Wrecsam | Llanfynydd STW | 5596 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330625 | 352031 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RH | LL116RH | ll11 6rh | ll116rh | Wrexham | Wrecsam | Llanfynydd STW | 5522 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330598 | 352102 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RL | LL116RL | ll11 6rl | ll116rl | Wrexham | Wrecsam | Llanfynydd STW | 5600 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330662 | 352051 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RN | LL116RN | ll11 6rn | ll116rn | Wrexham | Wrecsam | Llanfynydd STW | 5482 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330576 | 352136 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RP | LL116RP | ll11 6rp | ll116rp | Wrexham | Wrecsam | Gresford STW | 5434 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330807 | 352186 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RR | LL116RR | ll11 6rr | ll116rr | Wrexham | Wrecsam | Gresford STW | 5492 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330831 | 352073 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RS | LL116RS | ll11 6rs | ll116rs | Wrexham | Wrecsam | Gresford STW | 5509 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330747 | 352141 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RT | LL116RT | ll11 6rt | ll116rt | Wrexham | Wrecsam | Gresford STW | 5528 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330802 | 352051 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RU | LL116RU | ll11 6ru | ll116ru | Wrexham | Wrecsam | Gresford STW | 5573 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330698 | 352100 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RW | LL116RW | ll11 6rw | ll116rw | Wrexham | Wrecsam | Llanfynydd STW | 5525 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330682 | 352153 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6RY | LL116RY | ll11 6ry | ll116ry | Wrexham | Wrecsam | Gresford STW | 5571 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330737 | 352059 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SA | LL116SA | ll11 6sa | ll116sa | Wrexham | Wrecsam | Gresford STW | 5606 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330735 | 352009 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SB | LL116SB | ll11 6sb | ll116sb | Wrexham | Wrecsam | Gresford STW | 5621 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330767 | 351952 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SD | LL116SD | ll11 6sd | ll116sd | Wrexham | Wrecsam | Gresford STW | 5642 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330742 | 351948 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SE | LL116SE | ll11 6se | ll116se | Wrexham | Wrecsam | Gresford STW | 5671 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330807 | 351837 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SF | LL116SF | ll11 6sf | ll116sf | Wrexham | Wrecsam | Gresford STW | 5756 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330784 | 351739 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SG | LL116SG | ll11 6sg | ll116sg | Wrexham | Wrecsam | Gresford STW | 5954 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331047 | 351227 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SH | LL116SH | ll11 6sh | ll116sh | Wrexham | Wrecsam | Gresford STW | 5787 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330829 | 351650 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SJ | LL116SJ | ll11 6sj | ll116sj | Wrexham | Wrecsam | Gresford STW | 5827 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331034 | 351405 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SL | LL116SL | ll11 6sl | ll116sl | Wrexham | Wrecsam | Abenbury WwTW | 5490 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 331701 | 350965 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SN | LL116SN | ll11 6sn | ll116sn | Wrexham | Wrecsam | Gresford STW | 5959 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331150 | 351136 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SP | LL116SP | ll11 6sp | ll116sp | Wrexham | Wrecsam | Gresford STW | 5787 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331068 | 351428 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SR | LL116SR | ll11 6sr | ll116sr | Wrexham | Wrecsam | Gresford STW | 5774 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331121 | 351400 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SS | LL116SS | ll11 6ss | ll116ss | Wrexham | Wrecsam | Gresford STW | 5775 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331135 | 351386 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6ST | LL116ST | ll11 6st | ll116st | Wrexham | Wrecsam | Gresford STW | 5776 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331150 | 351372 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SU | LL116SU | ll11 6su | ll116su | Wrexham | Wrecsam | Gresford STW | 5804 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331117 | 351364 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SW | LL116SW | ll11 6sw | ll116sw | Wrexham | Wrecsam | Gresford STW | 5784 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331085 | 351418 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6SY | LL116SY | ll11 6sy | ll116sy | Wrexham | Wrecsam | Gresford STW | 5698 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331226 | 351410 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TA | LL116TA | ll11 6ta | ll116ta | Wrexham | Wrecsam | Gresford STW | 5695 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331203 | 351434 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TB | LL116TB | ll11 6tb | ll116tb | Wrexham | Wrecsam | Gresford STW | 5647 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331249 | 351458 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TD | LL116TD | ll11 6td | ll116td | Wrexham | Wrecsam | Gresford STW | 5830 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 330949 | 351477 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TE | LL116TE | ll11 6te | ll116te | Wrexham | Wrecsam | Gresford STW | 5805 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331003 | 351462 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TF | LL116TF | ll11 6tf | ll116tf | Wrexham | Wrecsam | Gresford STW | 5856 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331022 | 351377 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TG | LL116TG | ll11 6tg | ll116tg | Wrexham | Wrecsam | Gresford STW | 5896 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331051 | 351299 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TH | LL116TH | ll11 6th | ll116th | Wrexham | Wrecsam | Gresford STW | 5844 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331148 | 351285 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TJ | LL116TJ | ll11 6tj | ll116tj | Wrexham | Wrecsam | Gresford STW | 5926 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331076 | 351239 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TL | LL116TL | ll11 6tl | ll116tl | Wrexham | Wrecsam | Gresford STW | 5922 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331199 | 351144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TN | LL116TN | ll11 6tn | ll116tn | Wrexham | Wrecsam | Gresford STW | 5908 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331169 | 351185 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TP | LL116TP | ll11 6tp | ll116tp | Wrexham | Wrecsam | Gresford STW | 5831 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331325 | 351160 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TQ | LL116TQ | ll11 6tq | ll116tq | Wrexham | Wrecsam | Gresford STW | 5906 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331273 | 351106 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TR | LL116TR | ll11 6tr | ll116tr | Wrexham | Wrecsam | Gresford STW | 5785 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331232 | 351293 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TS | LL116TS | ll11 6ts | ll116ts | Wrexham | Wrecsam | Gresford STW | 5833 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331336 | 351150 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TT | LL116TT | ll11 6tt | ll116tt | Wrexham | Wrecsam | Gresford STW | 5841 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331344 | 351134 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TU | LL116TU | ll11 6tu | ll116tu | Wrexham | Wrecsam | Gresford STW | 5844 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331354 | 351122 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TW | LL116TW | ll11 6tw | ll116tw | Wrexham | Wrecsam | Gresford STW | 5856 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331212 | 351218 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TX | LL116TX | ll11 6tx | ll116tx | Wrexham | Wrecsam | Gresford STW | 5921 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 330873 | 351424 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TY | LL116TY | ll11 6ty | ll116ty | Wrexham | Wrecsam | Abenbury WwTW | 5807 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331401 | 351077 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6TZ | LL116TZ | ll11 6tz | ll116tz | Wrexham | Wrecsam | Gresford STW | 5824 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331184 | 351282 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UA | LL116UA | ll11 6ua | ll116ua | Wrexham | Wrecsam | Abenbury WwTW | 5772 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331426 | 351049 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UB | LL116UB | ll11 6ub | ll116ub | Wrexham | Wrecsam | Gresford STW | 5766 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331443 | 351153 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UD | LL116UD | ll11 6ud | ll116ud | Wrexham | Wrecsam | Gresford STW | 5765 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331389 | 351195 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UE | LL116UE | ll11 6ue | ll116ue | Wrexham | Wrecsam | Gresford STW | 5762 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331318 | 351254 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UF | LL116UF | ll11 6uf | ll116uf | Wrexham | Wrecsam | Gresford STW | 5719 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331217 | 351391 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UG | LL116UG | ll11 6ug | ll116ug | Wrexham | Wrecsam | Gresford STW | 5731 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331284 | 351320 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UH | LL116UH | ll11 6uh | ll116uh | Wrexham | Wrecsam | Gresford STW | 5704 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331248 | 351384 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UL | LL116UL | ll11 6ul | ll116ul | Wrexham | Wrecsam | Gresford STW | 5663 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331285 | 351407 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UN | LL116UN | ll11 6un | ll116un | Wrexham | Wrecsam | Gresford STW | 5676 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331313 | 351368 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UP | LL116UP | ll11 6up | ll116up | Wrexham | Wrecsam | Gresford STW | 5673 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331061 | 351587 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UR | LL116UR | ll11 6ur | ll116ur | Wrexham | Wrecsam | Gresford STW | 5683 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331101 | 351538 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6US | LL116US | ll11 6us | ll116us | Wrexham | Wrecsam | Gresford STW | 5682 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331119 | 351524 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UT | LL116UT | ll11 6ut | ll116ut | Wrexham | Wrecsam | Gresford STW | 5677 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331135 | 351516 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UU | LL116UU | ll11 6uu | ll116uu | Wrexham | Wrecsam | Gresford STW | 5669 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331164 | 351501 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UW | LL116UW | ll11 6uw | ll116uw | Wrexham | Wrecsam | Gresford STW | 5679 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331071 | 351570 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6UY | LL116UY | ll11 6uy | ll116uy | Wrexham | Wrecsam | Gresford STW | 5660 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331199 | 351483 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YA | LL116YA | ll11 6ya | ll116ya | Wrexham | Wrecsam | Abenbury WwTW | 5565 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 331732 | 351177 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YB | LL116YB | ll11 6yb | ll116yb | Wrexham | Wrecsam | Gresford STW | 5728 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331132 | 351451 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YD | LL116YD | ll11 6yd | ll116yd | Wrexham | Wrecsam | Gresford STW | 5732 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331112 | 351463 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YE | LL116YE | ll11 6ye | ll116ye | Wrexham | Wrecsam | Gresford STW | 5755 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331024 | 351511 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YF | LL116YF | ll11 6yf | ll116yf | Wrexham | Wrecsam | Gresford STW | 5650 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330917 | 351755 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YG | LL116YG | ll11 6yg | ll116yg | Wrexham | Wrecsam | Gresford STW | 5636 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330863 | 351830 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YJ | LL116YJ | ll11 6yj | ll116yj | Wrexham | Wrecsam | Gresford STW | 5695 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 331036 | 351580 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YL | LL116YL | ll11 6yl | ll116yl | Wrexham | Wrecsam | Gresford STW | 5519 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330924 | 351934 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YN | LL116YN | ll11 6yn | ll116yn | Wrexham | Wrecsam | Gresford STW | 5505 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330957 | 351920 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YP | LL116YP | ll11 6yp | ll116yp | Wrexham | Wrecsam | Gresford STW | 5686 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331379 | 351302 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YR | LL116YR | ll11 6yr | ll116yr | Wrexham | Wrecsam | Gresford STW | 5453 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330881 | 352075 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YS | LL116YS | ll11 6ys | ll116ys | Wrexham | Wrecsam | Gresford STW | 5861 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331096 | 351307 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YT | LL116YT | ll11 6yt | ll116yt | Wrexham | Wrecsam | Gresford STW | 5760 | 852 | 700to900 | 1.71 | 1.25 | 0.92 | 15.88 | 8.47 | 9.36 | 331047 | 351483 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YW | LL116YW | ll11 6yw | ll116yw | Wrexham | Wrecsam | Gresford STW | 5394 | 854 | 700to900 | 1.71 | 1.25 | 0.92 | 15.92 | 8.49 | 9.38 | 330910 | 352131 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL11 6YZ | LL116YZ | ll11 6yz | ll116yz | Wrexham | Wrecsam | Gresford STW | 5447 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 331555 | 351468 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AA | LL120AA | ll12 0aa | ll120aa | Wrexham | Wrecsam | Gresford STW | 1075 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 334857 | 356854 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AB | LL120AB | ll12 0ab | ll120ab | Wrexham | Wrecsam | Gresford STW | 1183 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334367 | 356845 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AD | LL120AD | ll12 0ad | ll120ad | Wrexham | Wrecsam | Gresford STW | 1740 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333952 | 357251 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AE | LL120AE | ll12 0ae | ll120ae | Wrexham | Wrecsam | Gresford STW | 1932 | 801 | 700to900 | 1.6 | 1.17 | 0.86 | 14.93 | 7.96 | 8.8 | 333414 | 357038 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AF | LL120AF | ll12 0af | ll120af | Wrexham | Wrecsam | Lavister WwTW | 2980 | 724 | 700to900 | 1.45 | 1.06 | 0.78 | 13.49 | 7.19 | 7.95 | 334835 | 359280 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AG | LL120AG | ll12 0ag | ll120ag | Wrexham | Wrecsam | Hope WwTW | 1949 | 810 | 700to900 | 1.62 | 1.19 | 0.87 | 15.1 | 8.05 | 8.9 | 332478 | 357734 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AH | LL120AH | ll12 0ah | ll120ah | Wrexham | Wrecsam | Gresford STW | 2540 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 333741 | 358049 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AJ | LL120AJ | ll12 0aj | ll120aj | Wrexham | Wrecsam | Gresford STW | 3421 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 334247 | 359141 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AL | LL120AL | ll12 0al | ll120al | Wrexham | Wrecsam | Gresford STW | 2850 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 333762 | 358400 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AN | LL120AN | ll12 0an | ll120an | Wrexham | Wrecsam | Hope WwTW | 2454 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 332887 | 358877 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AP | LL120AP | ll12 0ap | ll120ap | Wrexham | Wrecsam | Gresford STW | 3529 | 748 | 700to900 | 1.5 | 1.1 | 0.8 | 13.94 | 7.44 | 8.22 | 334182 | 359238 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AQ | LL120AQ | ll12 0aq | ll120aq | Wrexham | Wrecsam | Gresford STW | 2043 | 708 | 700to900 | 1.42 | 1.04 | 0.76 | 13.18 | 7.03 | 7.77 | 336798 | 356482 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AR | LL120AR | ll12 0ar | ll120ar | Wrexham | Wrecsam | Gresford STW | 2463 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335001 | 358239 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AS | LL120AS | ll12 0as | ll120as | Wrexham | Wrecsam | Lavister WwTW | 1875 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 335842 | 358599 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AT | LL120AT | ll12 0at | ll120at | Wrexham | Wrecsam | Lavister WwTW | 1449 | 712 | 700to900 | 1.42 | 1.04 | 0.76 | 13.26 | 7.07 | 7.82 | 336267 | 358565 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AU | LL120AU | ll12 0au | ll120au | Wrexham | Wrecsam | Lavister WwTW | 1102 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 336615 | 358586 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AW | LL120AW | ll12 0aw | ll120aw | Wrexham | Wrecsam | Gresford STW | 2674 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 334543 | 358432 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AX | LL120AX | ll12 0ax | ll120ax | Wrexham | Wrecsam | Lavister WwTW | 413 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337342 | 358343 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AY | LL120AY | ll12 0ay | ll120ay | Wrexham | Wrecsam | Lavister WwTW | 723 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337016 | 358335 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0AZ | LL120AZ | ll12 0az | ll120az | Wrexham | Wrecsam | Lavister WwTW | 1003 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337155 | 357687 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BA | LL120BA | ll12 0ba | ll120ba | Wrexham | Wrecsam | Lavister WwTW | 606 | 696 | 600to700 | 1.39 | 1.02 | 0.75 | 12.95 | 6.91 | 7.64 | 337766 | 357915 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BB | LL120BB | ll12 0bb | ll120bb | Wrexham | Wrecsam | Lavister WwTW | 636 | 696 | 600to700 | 1.39 | 1.02 | 0.75 | 12.95 | 6.91 | 7.64 | 337923 | 357918 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BD | LL120BD | ll12 0bd | ll120bd | Wrexham | Wrecsam | Lavister WwTW | 1361 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 338218 | 357255 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BE | LL120BE | ll12 0be | ll120be | Wrexham | Wrecsam | Lavister WwTW | 2113 | 696 | 600to700 | 1.39 | 1.02 | 0.75 | 12.95 | 6.91 | 7.64 | 338205 | 356464 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BF | LL120BF | ll12 0bf | ll120bf | Wrexham | Wrecsam | Lavister WwTW | 438 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337349 | 358279 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BG | LL120BG | ll12 0bg | ll120bg | Wrexham | Wrecsam | Gresford STW | 2428 | 708 | 700to900 | 1.42 | 1.04 | 0.76 | 13.18 | 7.03 | 7.77 | 337305 | 355892 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BH | LL120BH | ll12 0bh | ll120bh | Wrexham | Wrecsam | Gresford STW | 1878 | 708 | 700to900 | 1.42 | 1.04 | 0.76 | 13.18 | 7.03 | 7.77 | 336757 | 355769 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BJ | LL120BJ | ll12 0bj | ll120bj | Wrexham | Wrecsam | Lavister WwTW | 622 | 696 | 600to700 | 1.39 | 1.02 | 0.75 | 12.95 | 6.91 | 7.64 | 337534 | 357924 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BL | LL120BL | ll12 0bl | ll120bl | Wrexham | Wrecsam | Gresford STW | 2388 | 713 | 700to900 | 1.43 | 1.04 | 0.76 | 13.28 | 7.08 | 7.83 | 337024 | 354731 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BN | LL120BN | ll12 0bn | ll120bn | Wrexham | Wrecsam | Holt STW | 2173 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 338316 | 355265 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BP | LL120BP | ll12 0bp | ll120bp | Wrexham | Wrecsam | Holt STW | 2084 | 686 | 600to700 | 1.37 | 1 | 0.73 | 12.76 | 6.81 | 7.52 | 338648 | 355872 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BQ | LL120BQ | ll12 0bq | ll120bq | Wrexham | Wrecsam | Holt STW | 2543 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 337953 | 355334 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BS | LL120BS | ll12 0bs | ll120bs | Wrexham | Wrecsam | Lavister WwTW | 1882 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 338409 | 356770 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BT | LL120BT | ll12 0bt | ll120bt | Wrexham | Wrecsam | Lavister WwTW | 1932 | 682 | 600to700 | 1.36 | 1 | 0.73 | 12.68 | 6.76 | 7.48 | 338694 | 356854 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BU | LL120BU | ll12 0bu | ll120bu | Wrexham | Wrecsam | Holt STW | 1460 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 339764 | 356103 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BW | LL120BW | ll12 0bw | ll120bw | Wrexham | Wrecsam | Holt STW | 1798 | 688 | 600to700 | 1.37 | 1.01 | 0.74 | 12.8 | 6.83 | 7.54 | 338741 | 355395 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BX | LL120BX | ll12 0bx | ll120bx | Wrexham | Wrecsam | Gresford STW | 1970 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332912 | 355837 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0BY | LL120BY | ll12 0by | ll120by | Wrexham | Wrecsam | Holt STW | 1513 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 340440 | 356322 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DA | LL120DA | ll12 0da | ll120da | Wrexham | Wrecsam | Lavister WwTW | 633 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337180 | 358182 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DB | LL120DB | ll12 0db | ll120db | Wrexham | Wrecsam | Lavister WwTW | 1431 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336760 | 357454 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DD | LL120DD | ll12 0dd | ll120dd | Wrexham | Wrecsam | Lavister WwTW | 483 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337317 | 358245 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DE | LL120DE | ll12 0de | ll120de | Wrexham | Wrecsam | Lavister WwTW | 1353 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336856 | 357474 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DF | LL120DF | ll12 0df | ll120df | Wrexham | Wrecsam | Lavister WwTW | 582 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337229 | 358199 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DG | LL120DG | ll12 0dg | ll120dg | Wrexham | Wrecsam | Lavister WwTW | 1290 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336977 | 357461 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DH | LL120DH | ll12 0dh | ll120dh | Wrexham | Wrecsam | Lavister WwTW | 1107 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337079 | 357613 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DJ | LL120DJ | ll12 0dj | ll120dj | Wrexham | Wrecsam | Lavister WwTW | 1699 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336788 | 357096 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DL | LL120DL | ll12 0dl | ll120dl | Wrexham | Wrecsam | Lavister WwTW | 891 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337217 | 357781 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DN | LL120DN | ll12 0dn | ll120dn | Wrexham | Wrecsam | Lavister WwTW | 555 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337265 | 358195 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DP | LL120DP | ll12 0dp | ll120dp | Wrexham | Wrecsam | Lavister WwTW | 1350 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337004 | 357372 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DQ | LL120DQ | ll12 0dq | ll120dq | Wrexham | Wrecsam | Lavister WwTW | 1608 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 338103 | 356959 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DS | LL120DS | ll12 0ds | ll120ds | Wrexham | Wrecsam | Lavister WwTW | 1358 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336974 | 357381 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DT | LL120DT | ll12 0dt | ll120dt | Wrexham | Wrecsam | Lavister WwTW | 1413 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 337995 | 357135 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DU | LL120DU | ll12 0du | ll120du | Wrexham | Wrecsam | Lavister WwTW | 1415 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 338014 | 357136 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DW | LL120DW | ll12 0dw | ll120dw | Wrexham | Wrecsam | Lavister WwTW | 450 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337296 | 358356 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DX | LL120DX | ll12 0dx | ll120dx | Wrexham | Wrecsam | Lavister WwTW | 1452 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337108 | 357200 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DY | LL120DY | ll12 0dy | ll120dy | Wrexham | Wrecsam | Lavister WwTW | 1412 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 338034 | 357144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0DZ | LL120DZ | ll12 0dz | ll120dz | Wrexham | Wrecsam | Lavister WwTW | 1285 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337211 | 357337 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EA | LL120EA | ll12 0ea | ll120ea | Wrexham | Wrecsam | Lavister WwTW | 1320 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336990 | 357416 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EB | LL120EB | ll12 0eb | ll120eb | Wrexham | Wrecsam | Lavister WwTW | 1282 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337027 | 357438 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0ED | LL120ED | ll12 0ed | ll120ed | Wrexham | Wrecsam | Lavister WwTW | 1163 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337259 | 357450 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EE | LL120EE | ll12 0ee | ll120ee | Wrexham | Wrecsam | Lavister WwTW | 1237 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337061 | 357470 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EF | LL120EF | ll12 0ef | ll120ef | Wrexham | Wrecsam | Lavister WwTW | 1092 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337189 | 357562 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EG | LL120EG | ll12 0eg | ll120eg | Wrexham | Wrecsam | Lavister WwTW | 1037 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337223 | 357606 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EH | LL120EH | ll12 0eh | ll120eh | Wrexham | Wrecsam | Lavister WwTW | 1014 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337380 | 357562 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EJ | LL120EJ | ll12 0ej | ll120ej | Wrexham | Wrecsam | Lavister WwTW | 1348 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337136 | 357302 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EL | LL120EL | ll12 0el | ll120el | Wrexham | Wrecsam | Lavister WwTW | 666 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337422 | 357921 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EN | LL120EN | ll12 0en | ll120en | Wrexham | Wrecsam | Lavister WwTW | 694 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337391 | 357905 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EP | LL120EP | ll12 0ep | ll120ep | Wrexham | Wrecsam | Lavister WwTW | 1367 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 338018 | 357186 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EQ | LL120EQ | ll12 0eq | ll120eq | Wrexham | Wrecsam | Lavister WwTW | 1419 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337118 | 357232 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0ER | LL120ER | ll12 0er | ll120er | Wrexham | Wrecsam | Lavister WwTW | 1708 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 338156 | 356870 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0ES | LL120ES | ll12 0es | ll120es | Wrexham | Wrecsam | Lavister WwTW | 1820 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 337999 | 356722 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0ET | LL120ET | ll12 0et | ll120et | Wrexham | Wrecsam | Lavister WwTW | 1792 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 337892 | 356736 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EU | LL120EU | ll12 0eu | ll120eu | Wrexham | Wrecsam | Lavister WwTW | 1738 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 337698 | 356782 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EW | LL120EW | ll12 0ew | ll120ew | Wrexham | Wrecsam | Lavister WwTW | 865 | 696 | 600to700 | 1.39 | 1.02 | 0.75 | 12.95 | 6.91 | 7.64 | 337557 | 357669 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EX | LL120EX | ll12 0ex | ll120ex | Wrexham | Wrecsam | Lavister WwTW | 1362 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337052 | 357330 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EY | LL120EY | ll12 0ey | ll120ey | Wrexham | Wrecsam | Lavister WwTW | 1442 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336921 | 357316 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0EZ | LL120EZ | ll12 0ez | ll120ez | Wrexham | Wrecsam | Lavister WwTW | 1316 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337106 | 357353 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0FA | LL120FA | ll12 0fa | ll120fa | Wrexham | Wrecsam | Lavister WwTW | 761 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337478 | 357796 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0FB | LL120FB | ll12 0fb | ll120fb | Wrexham | Wrecsam | Lavister WwTW | 586 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337414 | 358017 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0FD | LL120FD | ll12 0fd | ll120fd | Wrexham | Wrecsam | Lavister WwTW | 632 | 696 | 600to700 | 1.39 | 1.02 | 0.75 | 12.95 | 6.91 | 7.64 | 337512 | 357921 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0GA | LL120GA | ll12 0ga | ll120ga | Wrexham | Wrecsam | Lavister WwTW | 566 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337327 | 358107 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0GB | LL120GB | ll12 0gb | ll120gb | Wrexham | Wrecsam | Gresford STW | 1443 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 335403 | 357124 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0GD | LL120GD | ll12 0gd | ll120gd | Wrexham | Wrecsam | Lavister WwTW | 1838 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 336419 | 357217 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HA | LL120HA | ll12 0ha | ll120ha | Wrexham | Wrecsam | Lavister WwTW | 1796 | 695 | 600to700 | 1.39 | 1.02 | 0.74 | 12.93 | 6.9 | 7.62 | 337932 | 356737 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HB | LL120HB | ll12 0hb | ll120hb | Wrexham | Wrecsam | Lavister WwTW | 1513 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337031 | 357170 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HD | LL120HD | ll12 0hd | ll120hd | Wrexham | Wrecsam | Lavister WwTW | 1508 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336897 | 357253 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HE | LL120HE | ll12 0he | ll120he | Wrexham | Wrecsam | Lavister WwTW | 1949 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 336343 | 357136 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HG | LL120HG | ll12 0hg | ll120hg | Wrexham | Wrecsam | Lavister WwTW | 1909 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 336345 | 357191 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HH | LL120HH | ll12 0hh | ll120hh | Wrexham | Wrecsam | Gresford STW | 1927 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336508 | 356809 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HJ | LL120HJ | ll12 0hj | ll120hj | Wrexham | Wrecsam | Lavister WwTW | 1623 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336758 | 357209 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HL | LL120HL | ll12 0hl | ll120hl | Wrexham | Wrecsam | Gresford STW | 1998 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336658 | 356689 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HN | LL120HN | ll12 0hn | ll120hn | Wrexham | Wrecsam | Lavister WwTW | 1697 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336621 | 357222 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HP | LL120HP | ll12 0hp | ll120hp | Wrexham | Wrecsam | Lavister WwTW | 1697 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336653 | 357196 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HQ | LL120HQ | ll12 0hq | ll120hq | Wrexham | Wrecsam | Lavister WwTW | 1586 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336873 | 357176 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HR | LL120HR | ll12 0hr | ll120hr | Wrexham | Wrecsam | Lavister WwTW | 1733 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336649 | 357153 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HS | LL120HS | ll12 0hs | ll120hs | Wrexham | Wrecsam | Gresford STW | 1526 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 335498 | 357175 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HT | LL120HT | ll12 0ht | ll120ht | Wrexham | Wrecsam | Gresford STW | 1212 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 335287 | 356921 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HU | LL120HU | ll12 0hu | ll120hu | Wrexham | Wrecsam | Gresford STW | 1836 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 335835 | 357347 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HW | LL120HW | ll12 0hw | ll120hw | Wrexham | Wrecsam | Lavister WwTW | 1612 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336745 | 357232 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HX | LL120HX | ll12 0hx | ll120hx | Wrexham | Wrecsam | Lavister WwTW | 1614 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336963 | 357092 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HY | LL120HY | ll12 0hy | ll120hy | Wrexham | Wrecsam | Gresford STW | 1928 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 335821 | 357462 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0HZ | LL120HZ | ll12 0hz | ll120hz | Wrexham | Wrecsam | Lavister WwTW | 1669 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336852 | 357091 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0JA | LL120JA | ll12 0ja | ll120ja | Wrexham | Wrecsam | Lavister WwTW | 1931 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 336267 | 357243 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LA | LL120LA | ll12 0la | ll120la | Wrexham | Wrecsam | Gresford STW | 1769 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335258 | 357508 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LB | LL120LB | ll12 0lb | ll120lb | Wrexham | Wrecsam | Gresford STW | 1582 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 335017 | 357356 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LD | LL120LD | ll12 0ld | ll120ld | Wrexham | Wrecsam | Gresford STW | 1618 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 334520 | 357357 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LE | LL120LE | ll12 0le | ll120le | Wrexham | Wrecsam | Gresford STW | 1574 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 334975 | 357351 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LF | LL120LF | ll12 0lf | ll120lf | Wrexham | Wrecsam | Gresford STW | 1634 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 335098 | 357399 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LG | LL120LG | ll12 0lg | ll120lg | Wrexham | Wrecsam | Gresford STW | 1862 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 335675 | 357463 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LH | LL120LH | ll12 0lh | ll120lh | Wrexham | Wrecsam | Gresford STW | 2033 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 335636 | 357666 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LL | LL120LL | ll12 0ll | ll120ll | Wrexham | Wrecsam | Gresford STW | 1558 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333389 | 355330 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LN | LL120LN | ll12 0ln | ll120ln | Wrexham | Wrecsam | Gresford STW | 1462 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333483 | 355349 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LP | LL120LP | ll12 0lp | ll120lp | Wrexham | Wrecsam | Gresford STW | 1390 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 333593 | 355256 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LR | LL120LR | ll12 0lr | ll120lr | Wrexham | Wrecsam | Gresford STW | 1316 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 333648 | 355319 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LS | LL120LS | ll12 0ls | ll120ls | Wrexham | Wrecsam | Gresford STW | 1110 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 333845 | 355380 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LT | LL120LT | ll12 0lt | ll120lt | Wrexham | Wrecsam | Gresford STW | 1158 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 333778 | 355425 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LU | LL120LU | ll12 0lu | ll120lu | Wrexham | Wrecsam | Gresford STW | 1328 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 333676 | 355221 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LW | LL120LW | ll12 0lw | ll120lw | Wrexham | Wrecsam | Gresford STW | 1294 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 333692 | 355268 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LX | LL120LX | ll12 0lx | ll120lx | Wrexham | Wrecsam | Gresford STW | 1640 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333274 | 356108 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LY | LL120LY | ll12 0ly | ll120ly | Wrexham | Wrecsam | Gresford STW | 1213 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 333785 | 355260 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0LZ | LL120LZ | ll12 0lz | ll120lz | Wrexham | Wrecsam | Gresford STW | 1536 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333398 | 356180 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NA | LL120NA | ll12 0na | ll120na | Wrexham | Wrecsam | Gresford STW | 1248 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 333718 | 355325 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NB | LL120NB | ll12 0nb | ll120nb | Wrexham | Wrecsam | Gresford STW | 1559 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333421 | 355231 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0ND | LL120ND | ll12 0nd | ll120nd | Wrexham | Wrecsam | Gresford STW | 1533 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333463 | 355196 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NE | LL120NE | ll12 0ne | ll120ne | Wrexham | Wrecsam | Gresford STW | 1462 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333495 | 356247 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NF | LL120NF | ll12 0nf | ll120nf | Wrexham | Wrecsam | Gresford STW | 1367 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 333641 | 355204 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NG | LL120NG | ll12 0ng | ll120ng | Wrexham | Wrecsam | Gresford STW | 1555 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333409 | 355276 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NH | LL120NH | ll12 0nh | ll120nh | Wrexham | Wrecsam | Gresford STW | 1433 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 333596 | 355144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NJ | LL120NJ | ll12 0nj | ll120nj | Wrexham | Wrecsam | Gresford STW | 1662 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333263 | 356162 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NL | LL120NL | ll12 0nl | ll120nl | Wrexham | Wrecsam | Gresford STW | 1409 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333488 | 355992 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NN | LL120NN | ll12 0nn | ll120nn | Wrexham | Wrecsam | Gresford STW | 1004 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333894 | 355968 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NQ | LL120NQ | ll12 0nq | ll120nq | Wrexham | Wrecsam | Gresford STW | 1543 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333377 | 356128 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NR | LL120NR | ll12 0nr | ll120nr | Wrexham | Wrecsam | Gresford STW | 775 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334118 | 355641 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NS | LL120NS | ll12 0ns | ll120ns | Wrexham | Wrecsam | Gresford STW | 886 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334014 | 355592 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NT | LL120NT | ll12 0nt | ll120nt | Wrexham | Wrecsam | Gresford STW | 1690 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333270 | 356293 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NU | LL120NU | ll12 0nu | ll120nu | Wrexham | Wrecsam | Gresford STW | 847 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334052 | 355959 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NW | LL120NW | ll12 0nw | ll120nw | Wrexham | Wrecsam | Gresford STW | 1207 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333696 | 356014 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NX | LL120NX | ll12 0nx | ll120nx | Wrexham | Wrecsam | Gresford STW | 1543 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333361 | 356050 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NY | LL120NY | ll12 0ny | ll120ny | Wrexham | Wrecsam | Gresford STW | 957 | 739 | 700to900 | 1.48 | 1.08 | 0.79 | 13.77 | 7.35 | 8.12 | 334623 | 356702 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0NZ | LL120NZ | ll12 0nz | ll120nz | Wrexham | Wrecsam | Gresford STW | 1465 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333440 | 356047 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PA | LL120PA | ll12 0pa | ll120pa | Wrexham | Wrecsam | Gresford STW | 1616 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333618 | 356789 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PB | LL120PB | ll12 0pb | ll120pb | Wrexham | Wrecsam | Gresford STW | 2283 | 801 | 700to900 | 1.6 | 1.17 | 0.86 | 14.93 | 7.96 | 8.8 | 332766 | 356639 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PD | LL120PD | ll12 0pd | ll120pd | Wrexham | Wrecsam | Hope WwTW | 2475 | 820 | 700to900 | 1.64 | 1.2 | 0.88 | 15.28 | 8.15 | 9.01 | 332115 | 356165 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PE | LL120PE | ll12 0pe | ll120pe | Wrexham | Wrecsam | Gresford STW | 1365 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333551 | 356088 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PG | LL120PG | ll12 0pg | ll120pg | Wrexham | Wrecsam | Hope WwTW | 2255 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 332273 | 356623 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PH | LL120PH | ll12 0ph | ll120ph | Wrexham | Wrecsam | Gresford STW | 1912 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332969 | 355747 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PJ | LL120PJ | ll12 0pj | ll120pj | Wrexham | Wrecsam | Gresford STW | 2524 | 820 | 700to900 | 1.64 | 1.2 | 0.88 | 15.28 | 8.15 | 9.01 | 332429 | 356380 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PL | LL120PL | ll12 0pl | ll120pl | Wrexham | Wrecsam | Gresford STW | 1688 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333223 | 355462 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PN | LL120PN | ll12 0pn | ll120pn | Wrexham | Wrecsam | Gresford STW | 1669 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333287 | 355284 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PP | LL120PP | ll12 0pp | ll120pp | Wrexham | Wrecsam | Gresford STW | 1591 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333435 | 355115 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PQ | LL120PQ | ll12 0pq | ll120pq | Wrexham | Wrecsam | Hope WwTW | 2430 | 820 | 700to900 | 1.64 | 1.2 | 0.88 | 15.28 | 8.15 | 9.01 | 332102 | 356212 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PR | LL120PR | ll12 0pr | ll120pr | Wrexham | Wrecsam | Gresford STW | 1800 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333086 | 355640 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PS | LL120PS | ll12 0ps | ll120ps | Wrexham | Wrecsam | Gresford STW | 1717 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333199 | 355435 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PT | LL120PT | ll12 0pt | ll120pt | Wrexham | Wrecsam | Gresford STW | 1893 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332988 | 355726 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PU | LL120PU | ll12 0pu | ll120pu | Wrexham | Wrecsam | Gresford STW | 1826 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333065 | 355587 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PW | LL120PW | ll12 0pw | ll120pw | Wrexham | Wrecsam | Gresford STW | 1672 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333344 | 355121 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PX | LL120PX | ll12 0px | ll120px | Wrexham | Wrecsam | Gresford STW | 1979 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332967 | 356286 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PY | LL120PY | ll12 0py | ll120py | Wrexham | Wrecsam | Gresford STW | 1939 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332945 | 355673 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0PZ | LL120PZ | ll12 0pz | ll120pz | Wrexham | Wrecsam | Gresford STW | 2085 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332821 | 356103 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QA | LL120QA | ll12 0qa | ll120qa | Wrexham | Wrecsam | Gresford STW | 1315 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333585 | 356003 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QB | LL120QB | ll12 0qb | ll120qb | Wrexham | Wrecsam | Hope WwTW | 1972 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 332298 | 357156 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QD | LL120QD | ll12 0qd | ll120qd | Wrexham | Wrecsam | Gresford STW | 1171 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333850 | 356337 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QE | LL120QE | ll12 0qe | ll120qe | Wrexham | Wrecsam | Gresford STW | 1465 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333516 | 356314 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QF | LL120QF | ll12 0qf | ll120qf | Wrexham | Wrecsam | Gresford STW | 1292 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333753 | 356411 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QH | LL120QH | ll12 0qh | ll120qh | Wrexham | Wrecsam | Gresford STW | 1102 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333873 | 356226 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QJ | LL120QJ | ll12 0qj | ll120qj | Wrexham | Wrecsam | Gresford STW | 1275 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333651 | 356118 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QN | LL120QN | ll12 0qn | ll120qn | Wrexham | Wrecsam | Gresford STW | 1038 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333909 | 356147 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QP | LL120QP | ll12 0qp | ll120qp | Wrexham | Wrecsam | Gresford STW | 1206 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333734 | 356154 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QQ | LL120QQ | ll12 0qq | ll120qq | Wrexham | Wrecsam | Gresford STW | 1205 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333708 | 356057 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QR | LL120QR | ll12 0qr | ll120qr | Wrexham | Wrecsam | Gresford STW | 1050 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333878 | 356091 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QS | LL120QS | ll12 0qs | ll120qs | Wrexham | Wrecsam | Gresford STW | 1420 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333592 | 356376 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QT | LL120QT | ll12 0qt | ll120qt | Wrexham | Wrecsam | Gresford STW | 1191 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333822 | 356327 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QU | LL120QU | ll12 0qu | ll120qu | Wrexham | Wrecsam | Gresford STW | 1255 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333701 | 356209 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QW | LL120QW | ll12 0qw | ll120qw | Wrexham | Wrecsam | Gresford STW | 1136 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333809 | 356158 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0QX | LL120QX | ll12 0qx | ll120qx | Wrexham | Wrecsam | Gresford STW | 1310 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333660 | 356257 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RA | LL120RA | ll12 0ra | ll120ra | Wrexham | Wrecsam | Gresford STW | 2015 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332882 | 355525 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RB | LL120RB | ll12 0rb | ll120rb | Wrexham | Wrecsam | Gresford STW | 2064 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332819 | 355690 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RD | LL120RD | ll12 0rd | ll120rd | Wrexham | Wrecsam | Gresford STW | 1966 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332921 | 355624 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RE | LL120RE | ll12 0re | ll120re | Wrexham | Wrecsam | Gresford STW | 1888 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332998 | 355641 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RF | LL120RF | ll12 0rf | ll120rf | Wrexham | Wrecsam | Gresford STW | 1981 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332912 | 355557 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RG | LL120RG | ll12 0rg | ll120rg | Wrexham | Wrecsam | Gresford STW | 1875 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333017 | 355570 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RH | LL120RH | ll12 0rh | ll120rh | Wrexham | Wrecsam | Gresford STW | 1926 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332973 | 355518 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RL | LL120RL | ll12 0rl | ll120rl | Wrexham | Wrecsam | Gresford STW | 1940 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 332988 | 355355 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RN | LL120RN | ll12 0rn | ll120rn | Wrexham | Wrecsam | Gresford STW | 1833 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333071 | 355488 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RP | LL120RP | ll12 0rp | ll120rp | Wrexham | Wrecsam | Gresford STW | 1967 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 332975 | 355291 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RR | LL120RR | ll12 0rr | ll120rr | Wrexham | Wrecsam | Gresford STW | 2037 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 332886 | 355366 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RS | LL120RS | ll12 0rs | ll120rs | Wrexham | Wrecsam | Gresford STW | 2056 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 332861 | 355396 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RT | LL120RT | ll12 0rt | ll120rt | Wrexham | Wrecsam | Gresford STW | 2066 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332833 | 355506 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RW | LL120RW | ll12 0rw | ll120rw | Wrexham | Wrecsam | Gresford STW | 1879 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333035 | 355430 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0RY | LL120RY | ll12 0ry | ll120ry | Wrexham | Wrecsam | Gresford STW | 966 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333920 | 355880 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SA | LL120SA | ll12 0sa | ll120sa | Wrexham | Wrecsam | Gresford STW | 1570 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333311 | 355745 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SB | LL120SB | ll12 0sb | ll120sb | Wrexham | Wrecsam | Gresford STW | 1479 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333402 | 355735 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SD | LL120SD | ll12 0sd | ll120sd | Wrexham | Wrecsam | Gresford STW | 1479 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333406 | 355667 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SE | LL120SE | ll12 0se | ll120se | Wrexham | Wrecsam | Gresford STW | 1375 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333506 | 355799 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SF | LL120SF | ll12 0sf | ll120sf | Wrexham | Wrecsam | Gresford STW | 1482 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333412 | 355578 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SG | LL120SG | ll12 0sg | ll120sg | Wrexham | Wrecsam | Gresford STW | 1513 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333399 | 355472 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SH | LL120SH | ll12 0sh | ll120sh | Wrexham | Wrecsam | Gresford STW | 1354 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333544 | 355560 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SJ | LL120SJ | ll12 0sj | ll120sj | Wrexham | Wrecsam | Gresford STW | 1507 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333378 | 355902 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SL | LL120SL | ll12 0sl | ll120sl | Wrexham | Wrecsam | Gresford STW | 1293 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333592 | 355673 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SN | LL120SN | ll12 0sn | ll120sn | Wrexham | Wrecsam | Gresford STW | 1381 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333509 | 355620 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SP | LL120SP | ll12 0sp | ll120sp | Wrexham | Wrecsam | Gresford STW | 1267 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333619 | 355665 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SQ | LL120SQ | ll12 0sq | ll120sq | Wrexham | Wrecsam | Gresford STW | 1282 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333616 | 355571 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SR | LL120SR | ll12 0sr | ll120sr | Wrexham | Wrecsam | Gresford STW | 1667 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333221 | 355622 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SS | LL120SS | ll12 0ss | ll120ss | Wrexham | Wrecsam | Gresford STW | 1725 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333166 | 355589 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0ST | LL120ST | ll12 0st | ll120st | Wrexham | Wrecsam | Gresford STW | 1754 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333127 | 355753 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SU | LL120SU | ll12 0su | ll120su | Wrexham | Wrecsam | Gresford STW | 1768 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333118 | 355638 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SW | LL120SW | ll12 0sw | ll120sw | Wrexham | Wrecsam | Gresford STW | 1396 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 333518 | 355478 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SX | LL120SX | ll12 0sx | ll120sx | Wrexham | Wrecsam | Gresford STW | 1568 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333314 | 355720 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SY | LL120SY | ll12 0sy | ll120sy | Wrexham | Wrecsam | Gresford STW | 1722 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333163 | 355660 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0SZ | LL120SZ | ll12 0sz | ll120sz | Wrexham | Wrecsam | Gresford STW | 1466 | 793 | 700to900 | 1.59 | 1.16 | 0.85 | 14.78 | 7.88 | 8.71 | 333451 | 355453 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TA | LL120TA | ll12 0ta | ll120ta | Wrexham | Wrecsam | Gresford STW | 1798 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333084 | 355723 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TB | LL120TB | ll12 0tb | ll120tb | Wrexham | Wrecsam | Gresford STW | 1690 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333191 | 355786 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TD | LL120TD | ll12 0td | ll120td | Wrexham | Wrecsam | Gresford STW | 1800 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333081 | 355799 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TE | LL120TE | ll12 0te | ll120te | Wrexham | Wrecsam | Gresford STW | 1899 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332983 | 355856 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TF | LL120TF | ll12 0tf | ll120tf | Wrexham | Wrecsam | Gresford STW | 1872 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333015 | 355928 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TH | LL120TH | ll12 0th | ll120th | Wrexham | Wrecsam | Gresford STW | 2293 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332588 | 355732 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TJ | LL120TJ | ll12 0tj | ll120tj | Wrexham | Wrecsam | Gresford STW | 1629 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333253 | 355701 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TL | LL120TL | ll12 0tl | ll120tl | Wrexham | Wrecsam | Gresford STW | 2371 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332523 | 356031 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TN | LL120TN | ll12 0tn | ll120tn | Wrexham | Wrecsam | Gresford STW | 1712 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333171 | 355873 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TP | LL120TP | ll12 0tp | ll120tp | Wrexham | Wrecsam | Gresford STW | 1635 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333246 | 355787 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TQ | LL120TQ | ll12 0tq | ll120tq | Wrexham | Wrecsam | Gresford STW | 1925 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332965 | 355973 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TR | LL120TR | ll12 0tr | ll120tr | Wrexham | Wrecsam | Gresford STW | 1647 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333249 | 356003 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TS | LL120TS | ll12 0ts | ll120ts | Wrexham | Wrecsam | Gresford STW | 1647 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333249 | 356003 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TT | LL120TT | ll12 0tt | ll120tt | Wrexham | Wrecsam | Gresford STW | 1385 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333496 | 355736 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TU | LL120TU | ll12 0tu | ll120tu | Wrexham | Wrecsam | Gresford STW | 1962 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 332953 | 356144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TW | LL120TW | ll12 0tw | ll120tw | Wrexham | Wrecsam | Gresford STW | 1875 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333016 | 355980 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TX | LL120TX | ll12 0tx | ll120tx | Wrexham | Wrecsam | Gresford STW | 1818 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333088 | 356084 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0TY | LL120TY | ll12 0ty | ll120ty | Wrexham | Wrecsam | Gresford STW | 1729 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333196 | 356169 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0UA | LL120UA | ll12 0ua | ll120ua | Wrexham | Wrecsam | Gresford STW | 1127 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333755 | 355840 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0UB | LL120UB | ll12 0ub | ll120ub | Wrexham | Wrecsam | Gresford STW | 1201 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333686 | 355909 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0UD | LL120UD | ll12 0ud | ll120ud | Wrexham | Wrecsam | Gresford STW | 1210 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333683 | 355951 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0UE | LL120UE | ll12 0ue | ll120ue | Wrexham | Wrecsam | Gresford STW | 1225 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333659 | 355868 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0UF | LL120UF | ll12 0uf | ll120uf | Wrexham | Wrecsam | Gresford STW | 1043 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333842 | 355879 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0UG | LL120UG | ll12 0ug | ll120ug | Wrexham | Wrecsam | Gresford STW | 2408 | 820 | 700to900 | 1.64 | 1.2 | 0.88 | 15.28 | 8.15 | 9.01 | 332491 | 356074 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0UL | LL120UL | ll12 0ul | ll120ul | Wrexham | Wrecsam | Gresford STW | 1034 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333846 | 355780 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0UN | LL120UN | ll12 0un | ll120un | Wrexham | Wrecsam | Gresford STW | 966 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333914 | 355797 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0UR | LL120UR | ll12 0ur | ll120ur | Wrexham | Wrecsam | Gresford STW | 1876 | 796 | 700to900 | 1.59 | 1.17 | 0.85 | 14.84 | 7.91 | 8.75 | 333005 | 355795 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0UW | LL120UW | ll12 0uw | ll120uw | Wrexham | Wrecsam | Gresford STW | 853 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334027 | 355781 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 0UX | LL120UX | ll12 0ux | ll120ux | Wrexham | Wrecsam | Gresford STW | 840 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334043 | 355716 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AA | LL127AA | ll12 7aa | ll127aa | Wrexham | Wrecsam | Abenbury WwTW | 3848 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333427 | 350644 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AB | LL127AB | ll12 7ab | ll127ab | Wrexham | Wrecsam | Abenbury WwTW | 3867 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333458 | 350717 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AD | LL127AD | ll12 7ad | ll127ad | Wrexham | Wrecsam | Abenbury WwTW | 3733 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333630 | 350721 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AE | LL127AE | ll12 7ae | ll127ae | Wrexham | Wrecsam | Abenbury WwTW | 3729 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333664 | 350758 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AG | LL127AG | ll12 7ag | ll127ag | Wrexham | Wrecsam | Abenbury WwTW | 3605 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333752 | 350670 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AH | LL127AH | ll12 7ah | ll127ah | Wrexham | Wrecsam | Abenbury WwTW | 3646 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333904 | 350906 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AJ | LL127AJ | ll12 7aj | ll127aj | Wrexham | Wrecsam | Abenbury WwTW | 3836 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333828 | 351100 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AL | LL127AL | ll12 7al | ll127al | Wrexham | Wrecsam | Abenbury WwTW | 3691 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334008 | 351074 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AN | LL127AN | ll12 7an | ll127an | Wrexham | Wrecsam | Abenbury WwTW | 3685 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334170 | 351211 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AP | LL127AP | ll12 7ap | ll127ap | Wrexham | Wrecsam | Abenbury WwTW | 3766 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333898 | 351071 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AR | LL127AR | ll12 7ar | ll127ar | Wrexham | Wrecsam | Abenbury WwTW | 3848 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333694 | 350976 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AS | LL127AS | ll12 7as | ll127as | Wrexham | Wrecsam | Abenbury WwTW | 3936 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333706 | 351118 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AT | LL127AT | ll12 7at | ll127at | Wrexham | Wrecsam | Abenbury WwTW | 3788 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334003 | 351202 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AU | LL127AU | ll12 7au | ll127au | Wrexham | Wrecsam | Abenbury WwTW | 3811 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333928 | 351163 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AW | LL127AW | ll12 7aw | ll127aw | Wrexham | Wrecsam | Abenbury WwTW | 3756 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334135 | 351275 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AX | LL127AX | ll12 7ax | ll127ax | Wrexham | Wrecsam | Abenbury WwTW | 3821 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333588 | 350810 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AY | LL127AY | ll12 7ay | ll127ay | Wrexham | Wrecsam | Abenbury WwTW | 3750 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333954 | 351104 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7AZ | LL127AZ | ll12 7az | ll127az | Wrexham | Wrecsam | Abenbury WwTW | 3562 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333913 | 350791 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BA | LL127BA | ll12 7ba | ll127ba | Wrexham | Wrecsam | Abenbury WwTW | 3872 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333961 | 351277 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BB | LL127BB | ll12 7bb | ll127bb | Wrexham | Wrecsam | Abenbury WwTW | 3727 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334348 | 351405 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BD | LL127BD | ll12 7bd | ll127bd | Wrexham | Wrecsam | Abenbury WwTW | 3777 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334310 | 351439 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BE | LL127BE | ll12 7be | ll127be | Wrexham | Wrecsam | Abenbury WwTW | 3894 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334116 | 351437 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BG | LL127BG | ll12 7bg | ll127bg | Wrexham | Wrecsam | Abenbury WwTW | 3839 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334205 | 351438 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BH | LL127BH | ll12 7bh | ll127bh | Wrexham | Wrecsam | Abenbury WwTW | 4078 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333758 | 351370 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BJ | LL127BJ | ll12 7bj | ll127bj | Wrexham | Wrecsam | Abenbury WwTW | 3802 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334077 | 351286 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BL | LL127BL | ll12 7bl | ll127bl | Wrexham | Wrecsam | Abenbury WwTW | 4015 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333886 | 351402 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BN | LL127BN | ll12 7bn | ll127bn | Wrexham | Wrecsam | Abenbury WwTW | 3929 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334040 | 351420 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BP | LL127BP | ll12 7bp | ll127bp | Wrexham | Wrecsam | Abenbury WwTW | 3548 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333763 | 350591 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BS | LL127BS | ll12 7bs | ll127bs | Wrexham | Wrecsam | Abenbury WwTW | 3560 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334035 | 350917 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BT | LL127BT | ll12 7bt | ll127bt | Wrexham | Wrecsam | Abenbury WwTW | 3593 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334018 | 350946 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BU | LL127BU | ll12 7bu | ll127bu | Wrexham | Wrecsam | Abenbury WwTW | 3469 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334061 | 350813 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7BY | LL127BY | ll12 7by | ll127by | Wrexham | Wrecsam | Abenbury WwTW | 3528 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334053 | 350889 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DA | LL127DA | ll12 7da | ll127da | Wrexham | Wrecsam | Abenbury WwTW | 3506 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334097 | 350902 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DB | LL127DB | ll12 7db | ll127db | Wrexham | Wrecsam | Abenbury WwTW | 3393 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334172 | 350817 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DD | LL127DD | ll12 7dd | ll127dd | Wrexham | Wrecsam | Abenbury WwTW | 3504 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334124 | 350926 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DE | LL127DE | ll12 7de | ll127de | Wrexham | Wrecsam | Abenbury WwTW | 3626 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334052 | 351026 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DF | LL127DF | ll12 7df | ll127df | Wrexham | Wrecsam | Abenbury WwTW | 3494 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334158 | 350944 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DG | LL127DG | ll12 7dg | ll127dg | Wrexham | Wrecsam | Abenbury WwTW | 3589 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334239 | 351144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DH | LL127DH | ll12 7dh | ll127dh | Wrexham | Wrecsam | Abenbury WwTW | 3566 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334227 | 351104 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DJ | LL127DJ | ll12 7dj | ll127dj | Wrexham | Wrecsam | Abenbury WwTW | 3364 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334171 | 350776 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DL | LL127DL | ll12 7dl | ll127dl | Wrexham | Wrecsam | Abenbury WwTW | 3379 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334359 | 350971 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DN | LL127DN | ll12 7dn | ll127dn | Wrexham | Wrecsam | Abenbury WwTW | 3505 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334221 | 351017 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DP | LL127DP | ll12 7dp | ll127dp | Wrexham | Wrecsam | Abenbury WwTW | 3521 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334229 | 351046 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DR | LL127DR | ll12 7dr | ll127dr | Wrexham | Wrecsam | Abenbury WwTW | 3491 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334189 | 350969 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DS | LL127DS | ll12 7ds | ll127ds | Wrexham | Wrecsam | Abenbury WwTW | 3369 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334247 | 350856 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DT | LL127DT | ll12 7dt | ll127dt | Wrexham | Wrecsam | Abenbury WwTW | 3419 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334281 | 350955 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DU | LL127DU | ll12 7du | ll127du | Wrexham | Wrecsam | Abenbury WwTW | 3476 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334313 | 351058 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DW | LL127DW | ll12 7dw | ll127dw | Wrexham | Wrecsam | Abenbury WwTW | 3388 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334378 | 350998 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7DY | LL127DY | ll12 7dy | ll127dy | Wrexham | Wrecsam | Abenbury WwTW | 3554 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334307 | 351155 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7EA | LL127EA | ll12 7ea | ll127ea | Wrexham | Wrecsam | Abenbury WwTW | 3352 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334287 | 350871 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7EB | LL127EB | ll12 7eb | ll127eb | Wrexham | Wrecsam | Abenbury WwTW | 3456 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334408 | 351111 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7ED | LL127ED | ll12 7ed | ll127ed | Wrexham | Wrecsam | Abenbury WwTW | 3414 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334379 | 351033 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7EE | LL127EE | ll12 7ee | ll127ee | Wrexham | Wrecsam | Abenbury WwTW | 3363 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334348 | 350940 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7EF | LL127EF | ll12 7ef | ll127ef | Wrexham | Wrecsam | Abenbury WwTW | 3494 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334621 | 351312 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7EG | LL127EG | ll12 7eg | ll127eg | Wrexham | Wrecsam | Abenbury WwTW | 3318 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334361 | 350892 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7EH | LL127EH | ll12 7eh | ll127eh | Wrexham | Wrecsam | Abenbury WwTW | 3373 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334462 | 351048 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7EL | LL127EL | ll12 7el | ll127el | Wrexham | Wrecsam | Abenbury WwTW | 3394 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334487 | 351093 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7EN | LL127EN | ll12 7en | ll127en | Wrexham | Wrecsam | Abenbury WwTW | 3430 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334560 | 351193 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7EP | LL127EP | ll12 7ep | ll127ep | Wrexham | Wrecsam | Abenbury WwTW | 3336 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334486 | 351019 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7ER | LL127ER | ll12 7er | ll127er | Wrexham | Wrecsam | Abenbury WwTW | 3477 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334725 | 351359 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7EU | LL127EU | ll12 7eu | ll127eu | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333704 | 351428 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7EW | LL127EW | ll12 7ew | ll127ew | Wrexham | Wrecsam | Abenbury WwTW | 3488 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334672 | 351338 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7EY | LL127EY | ll12 7ey | ll127ey | Wrexham | Wrecsam | Abenbury WwTW | 4209 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333660 | 351457 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HA | LL127HA | ll12 7ha | ll127ha | Wrexham | Wrecsam | Abenbury WwTW | 4239 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333709 | 351543 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HB | LL127HB | ll12 7hb | ll127hb | Wrexham | Wrecsam | Abenbury WwTW | 4206 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333689 | 351480 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HD | LL127HD | ll12 7hd | ll127hd | Wrexham | Wrecsam | Abenbury WwTW | 4103 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333810 | 351452 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HE | LL127HE | ll12 7he | ll127he | Wrexham | Wrecsam | Abenbury WwTW | 4164 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333813 | 351536 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HF | LL127HF | ll12 7hf | ll127hf | Wrexham | Wrecsam | Abenbury WwTW | 4068 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333818 | 351412 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HG | LL127HG | ll12 7hg | ll127hg | Wrexham | Wrecsam | Abenbury WwTW | 4065 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333868 | 351452 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HH | LL127HH | ll12 7hh | ll127hh | Wrexham | Wrecsam | Abenbury WwTW | 4051 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333936 | 351492 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HL | LL127HL | ll12 7hl | ll127hl | Wrexham | Wrecsam | Abenbury WwTW | 4086 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333947 | 351547 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HN | LL127HN | ll12 7hn | ll127hn | Wrexham | Wrecsam | Abenbury WwTW | 3911 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334185 | 351513 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HP | LL127HP | ll12 7hp | ll127hp | Wrexham | Wrecsam | Abenbury WwTW | 4018 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333947 | 351458 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HR | LL127HR | ll12 7hr | ll127hr | Wrexham | Wrecsam | Abenbury WwTW | 3936 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334095 | 351474 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HS | LL127HS | ll12 7hs | ll127hs | Wrexham | Wrecsam | Abenbury WwTW | 4046 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334038 | 351570 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HT | LL127HT | ll12 7ht | ll127ht | Wrexham | Wrecsam | Abenbury WwTW | 4137 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334023 | 351673 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HU | LL127HU | ll12 7hu | ll127hu | Wrexham | Wrecsam | Gresford STW | 4109 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333945 | 351780 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HW | LL127HW | ll12 7hw | ll127hw | Wrexham | Wrecsam | Abenbury WwTW | 3976 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334119 | 351545 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7HY | LL127HY | ll12 7hy | ll127hy | Wrexham | Wrecsam | Abenbury WwTW | 3911 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334146 | 351483 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LA | LL127LA | ll12 7la | ll127la | Wrexham | Wrecsam | Abenbury WwTW | 3999 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334131 | 351582 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LB | LL127LB | ll12 7lb | ll127lb | Wrexham | Wrecsam | Abenbury WwTW | 4122 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334098 | 351712 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LD | LL127LD | ll12 7ld | ll127ld | Wrexham | Wrecsam | Gresford STW | 4121 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334051 | 351745 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LE | LL127LE | ll12 7le | ll127le | Wrexham | Wrecsam | Abenbury WwTW | 4216 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333878 | 351659 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LF | LL127LF | ll12 7lf | ll127lf | Wrexham | Wrecsam | Abenbury WwTW | 4291 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333707 | 351612 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LG | LL127LG | ll12 7lg | ll127lg | Wrexham | Wrecsam | Gresford STW | 4075 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334039 | 351794 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LJ | LL127LJ | ll12 7lj | ll127lj | Wrexham | Wrecsam | Abenbury WwTW | 3840 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334106 | 351360 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LN | LL127LN | ll12 7ln | ll127ln | Wrexham | Wrecsam | Abenbury WwTW | 3684 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334240 | 351268 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LP | LL127LP | ll12 7lp | ll127lp | Wrexham | Wrecsam | Abenbury WwTW | 3501 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334442 | 351194 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LR | LL127LR | ll12 7lr | ll127lr | Wrexham | Wrecsam | Abenbury WwTW | 3709 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334271 | 351325 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LS | LL127LS | ll12 7ls | ll127ls | Wrexham | Wrecsam | Abenbury WwTW | 3585 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334423 | 351284 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LT | LL127LT | ll12 7lt | ll127lt | Wrexham | Wrecsam | Abenbury WwTW | 3522 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334465 | 351237 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LU | LL127LU | ll12 7lu | ll127lu | Wrexham | Wrecsam | Abenbury WwTW | 3520 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334514 | 351270 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LW | LL127LW | ll12 7lw | ll127lw | Wrexham | Wrecsam | Abenbury WwTW | 3565 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334335 | 351192 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7LY | LL127LY | ll12 7ly | ll127ly | Wrexham | Wrecsam | Abenbury WwTW | 3939 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333952 | 351359 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NA | LL127NA | ll12 7na | ll127na | Wrexham | Wrecsam | Abenbury WwTW | 3714 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334313 | 351363 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NB | LL127NB | ll12 7nb | ll127nb | Wrexham | Wrecsam | Abenbury WwTW | 3608 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334603 | 351437 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NF | LL127NF | ll12 7nf | ll127nf | Wrexham | Wrecsam | Abenbury WwTW | 3727 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334431 | 351465 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NG | LL127NG | ll12 7ng | ll127ng | Wrexham | Wrecsam | Abenbury WwTW | 3815 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334323 | 351496 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NH | LL127NH | ll12 7nh | ll127nh | Wrexham | Wrecsam | Abenbury WwTW | 3795 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334421 | 351540 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NJ | LL127NJ | ll12 7nj | ll127nj | Wrexham | Wrecsam | Abenbury WwTW | 3872 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334057 | 351360 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NL | LL127NL | ll12 7nl | ll127nl | Wrexham | Wrecsam | Abenbury WwTW | 3762 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334438 | 351512 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NN | LL127NN | ll12 7nn | ll127nn | Wrexham | Wrecsam | Abenbury WwTW | 3777 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334588 | 351626 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NP | LL127NP | ll12 7np | ll127np | Wrexham | Wrecsam | Abenbury WwTW | 3856 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334221 | 351471 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NR | LL127NR | ll12 7nr | ll127nr | Wrexham | Wrecsam | Abenbury WwTW | 3939 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334275 | 351614 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NS | LL127NS | ll12 7ns | ll127ns | Wrexham | Wrecsam | Abenbury WwTW | 3911 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334372 | 351647 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NT | LL127NT | ll12 7nt | ll127nt | Wrexham | Wrecsam | Abenbury WwTW | 4007 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334219 | 351658 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NU | LL127NU | ll12 7nu | ll127nu | Wrexham | Wrecsam | Abenbury WwTW | 4047 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334219 | 351707 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7NW | LL127NW | ll12 7nw | ll127nw | Wrexham | Wrecsam | Abenbury WwTW | 3854 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334377 | 351582 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PB | LL127PB | ll12 7pb | ll127pb | Wrexham | Wrecsam | Abenbury WwTW | 3813 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334811 | 351793 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PD | LL127PD | ll12 7pd | ll127pd | Wrexham | Wrecsam | Gresford STW | 3758 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334711 | 352027 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PE | LL127PE | ll12 7pe | ll127pe | Wrexham | Wrecsam | Gresford STW | 3467 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334551 | 352330 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PF | LL127PF | ll12 7pf | ll127pf | Wrexham | Wrecsam | Gresford STW | 3324 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334443 | 352486 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PG | LL127PG | ll12 7pg | ll127pg | Wrexham | Wrecsam | Gresford STW | 3356 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334378 | 352463 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PH | LL127PH | ll12 7ph | ll127ph | Wrexham | Wrecsam | Gresford STW | 3297 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334579 | 352498 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PL | LL127PL | ll12 7pl | ll127pl | Wrexham | Wrecsam | Gresford STW | 3379 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334562 | 352417 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PN | LL127PN | ll12 7pn | ll127pn | Wrexham | Wrecsam | Gresford STW | 3165 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 334649 | 352625 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PP | LL127PP | ll12 7pp | ll127pp | Wrexham | Wrecsam | Gresford STW | 3188 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 334566 | 352609 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PR | LL127PR | ll12 7pr | ll127pr | Wrexham | Wrecsam | Gresford STW | 3163 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 334528 | 352638 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PS | LL127PS | ll12 7ps | ll127ps | Wrexham | Wrecsam | Gresford STW | 3207 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334458 | 352602 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PT | LL127PT | ll12 7pt | ll127pt | Wrexham | Wrecsam | Gresford STW | 3208 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334390 | 352611 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PU | LL127PU | ll12 7pu | ll127pu | Wrexham | Wrecsam | Gresford STW | 3148 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334296 | 352688 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PW | LL127PW | ll12 7pw | ll127pw | Wrexham | Wrecsam | Gresford STW | 3221 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 334611 | 352571 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7PY | LL127PY | ll12 7py | ll127py | Wrexham | Wrecsam | Gresford STW | 3241 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334292 | 352594 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RA | LL127RA | ll12 7ra | ll127ra | Wrexham | Wrecsam | Gresford STW | 3187 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334326 | 352643 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RB | LL127RB | ll12 7rb | ll127rb | Wrexham | Wrecsam | Gresford STW | 3555 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334136 | 352305 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RD | LL127RD | ll12 7rd | ll127rd | Wrexham | Wrecsam | Gresford STW | 3179 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334240 | 352667 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RE | LL127RE | ll12 7re | ll127re | Wrexham | Wrecsam | Gresford STW | 3621 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334252 | 352215 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RF | LL127RF | ll12 7rf | ll127rf | Wrexham | Wrecsam | Gresford STW | 3387 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334281 | 352448 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RG | LL127RG | ll12 7rg | ll127rg | Wrexham | Wrecsam | Gresford STW | 3632 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334211 | 352211 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RH | LL127RH | ll12 7rh | ll127rh | Wrexham | Wrecsam | Gresford STW | 3523 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334286 | 352309 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RL | LL127RL | ll12 7rl | ll127rl | Wrexham | Wrecsam | Gresford STW | 3356 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334198 | 352495 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RN | LL127RN | ll12 7rn | ll127rn | Wrexham | Wrecsam | Gresford STW | 3815 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334778 | 351968 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RP | LL127RP | ll12 7rp | ll127rp | Wrexham | Wrecsam | Abenbury WwTW | 3840 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334982 | 351905 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RR | LL127RR | ll12 7rr | ll127rr | Wrexham | Wrecsam | Gresford STW | 3818 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334919 | 351964 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RS | LL127RS | ll12 7rs | ll127rs | Wrexham | Wrecsam | Gresford STW | 3852 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334905 | 351929 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RT | LL127RT | ll12 7rt | ll127rt | Wrexham | Wrecsam | Gresford STW | 3712 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334742 | 352072 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RU | LL127RU | ll12 7ru | ll127ru | Wrexham | Wrecsam | Gresford STW | 3702 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334785 | 352081 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RW | LL127RW | ll12 7rw | ll127rw | Wrexham | Wrecsam | Abenbury WwTW | 3853 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334878 | 351871 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7RY | LL127RY | ll12 7ry | ll127ry | Wrexham | Wrecsam | Gresford STW | 3377 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334673 | 352411 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SA | LL127SA | ll12 7sa | ll127sa | Wrexham | Wrecsam | Gresford STW | 3235 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 334727 | 352550 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SB | LL127SB | ll12 7sb | ll127sb | Wrexham | Wrecsam | Gresford STW | 3484 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334610 | 352308 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SD | LL127SD | ll12 7sd | ll127sd | Wrexham | Wrecsam | Gresford STW | 3262 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 334692 | 352525 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SE | LL127SE | ll12 7se | ll127se | Wrexham | Wrecsam | Gresford STW | 3759 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334948 | 352023 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SF | LL127SF | ll12 7sf | ll127sf | Wrexham | Wrecsam | Gresford STW | 3678 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334826 | 352104 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SG | LL127SG | ll12 7sg | ll127sg | Wrexham | Wrecsam | Gresford STW | 3599 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334891 | 352182 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SH | LL127SH | ll12 7sh | ll127sh | Wrexham | Wrecsam | Gresford STW | 3566 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334734 | 352218 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SL | LL127SL | ll12 7sl | ll127sl | Wrexham | Wrecsam | Gresford STW | 3480 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334690 | 352306 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SN | LL127SN | ll12 7sn | ll127sn | Wrexham | Wrecsam | Gresford STW | 3436 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334698 | 352350 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SP | LL127SP | ll12 7sp | ll127sp | Wrexham | Wrecsam | Gresford STW | 3333 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334632 | 352457 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SR | LL127SR | ll12 7sr | ll127sr | Wrexham | Wrecsam | Gresford STW | 3312 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334782 | 352471 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SS | LL127SS | ll12 7ss | ll127ss | Wrexham | Wrecsam | Gresford STW | 3235 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 334809 | 352547 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7ST | LL127ST | ll12 7st | ll127st | Wrexham | Wrecsam | Gresford STW | 3415 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334792 | 352367 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7SW | LL127SW | ll12 7sw | ll127sw | Wrexham | Wrecsam | Gresford STW | 3430 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334567 | 352366 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TD | LL127TD | ll12 7td | ll127td | Wrexham | Wrecsam | Abenbury WwTW | 3691 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334810 | 351654 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TE | LL127TE | ll12 7te | ll127te | Wrexham | Wrecsam | Abenbury WwTW | 3774 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334916 | 351802 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TF | LL127TF | ll12 7tf | ll127tf | Wrexham | Wrecsam | Gresford STW | 3809 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335084 | 351978 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TG | LL127TG | ll12 7tg | ll127tg | Wrexham | Wrecsam | Abenbury WwTW | 3711 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334902 | 351725 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TH | LL127TH | ll12 7th | ll127th | Wrexham | Wrecsam | Abenbury WwTW | 3754 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335006 | 351821 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TJ | LL127TJ | ll12 7tj | ll127tj | Wrexham | Wrecsam | Gresford STW | 3638 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335141 | 352153 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TL | LL127TL | ll12 7tl | ll127tl | Wrexham | Wrecsam | Abenbury WwTW | 3686 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335061 | 351772 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TN | LL127TN | ll12 7tn | ll127tn | Wrexham | Wrecsam | Abenbury WwTW | 3597 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334992 | 351642 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TP | LL127TP | ll12 7tp | ll127tp | Wrexham | Wrecsam | Abenbury WwTW | 3444 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335259 | 351593 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TQ | LL127TQ | ll12 7tq | ll127tq | Wrexham | Wrecsam | Gresford STW | 3597 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335186 | 352197 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TR | LL127TR | ll12 7tr | ll127tr | Wrexham | Wrecsam | Abenbury WwTW | 3583 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335116 | 351683 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TS | LL127TS | ll12 7ts | ll127ts | Wrexham | Wrecsam | Abenbury WwTW | 3525 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335169 | 351643 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TT | LL127TT | ll12 7tt | ll127tt | Wrexham | Wrecsam | Abenbury WwTW | 3618 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335026 | 351681 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TU | LL127TU | ll12 7tu | ll127tu | Wrexham | Wrecsam | Gresford STW | 3706 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335040 | 352079 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TW | LL127TW | ll12 7tw | ll127tw | Wrexham | Wrecsam | Abenbury WwTW | 3459 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335111 | 351545 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TX | LL127TX | ll12 7tx | ll127tx | Wrexham | Wrecsam | Gresford STW | 3633 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335262 | 352168 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7TY | LL127TY | ll12 7ty | ll127ty | Wrexham | Wrecsam | Gresford STW | 3789 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334986 | 351994 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7UA | LL127UA | ll12 7ua | ll127ua | Wrexham | Wrecsam | Gresford STW | 3737 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335121 | 352052 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7UB | LL127UB | ll12 7ub | ll127ub | Wrexham | Wrecsam | Gresford STW | 3634 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335090 | 352153 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7UD | LL127UD | ll12 7ud | ll127ud | Wrexham | Wrecsam | Gresford STW | 3753 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334857 | 352028 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7UE | LL127UE | ll12 7ue | ll127ue | Wrexham | Wrecsam | Gresford STW | 3521 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334989 | 352262 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7UF | LL127UF | ll12 7uf | ll127uf | Wrexham | Wrecsam | Gresford STW | 3538 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334964 | 352244 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7UG | LL127UG | ll12 7ug | ll127ug | Wrexham | Wrecsam | Gresford STW | 3556 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334823 | 352226 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7UH | LL127UH | ll12 7uh | ll127uh | Wrexham | Wrecsam | Gresford STW | 3458 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334986 | 352325 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7UP | LL127UP | ll12 7up | ll127up | Wrexham | Wrecsam | Abenbury WwTW | 3893 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334458 | 351682 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7UR | LL127UR | ll12 7ur | ll127ur | Wrexham | Wrecsam | Abenbury WwTW | 4004 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334389 | 351770 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7US | LL127US | ll12 7us | ll127us | Wrexham | Wrecsam | Abenbury WwTW | 3920 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334501 | 351741 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7UT | LL127UT | ll12 7ut | ll127ut | Wrexham | Wrecsam | Abenbury WwTW | 3880 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334442 | 351656 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7UU | LL127UU | ll12 7uu | ll127uu | Wrexham | Wrecsam | Abenbury WwTW | 3884 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334623 | 351771 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7UY | LL127UY | ll12 7uy | ll127uy | Wrexham | Wrecsam | Abenbury WwTW | 3876 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334647 | 351776 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YA | LL127YA | ll12 7ya | ll127ya | Wrexham | Wrecsam | Gresford STW | 3989 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334473 | 351813 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YB | LL127YB | ll12 7yb | ll127yb | Wrexham | Wrecsam | Gresford STW | 4045 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334050 | 351822 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YD | LL127YD | ll12 7yd | ll127yd | Wrexham | Wrecsam | Gresford STW | 4003 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334034 | 351869 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YE | LL127YE | ll12 7ye | ll127ye | Wrexham | Wrecsam | Gresford STW | 4053 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333888 | 351852 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YF | LL127YF | ll12 7yf | ll127yf | Wrexham | Wrecsam | Abenbury WwTW | 3760 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334685 | 351664 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YG | LL127YG | ll12 7yg | ll127yg | Wrexham | Wrecsam | Abenbury WwTW | 3961 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334567 | 351828 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YH | LL127YH | ll12 7yh | ll127yh | Wrexham | Wrecsam | Gresford STW | 3957 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334006 | 351922 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YJ | LL127YJ | ll12 7yj | ll127yj | Wrexham | Wrecsam | Gresford STW | 3841 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334249 | 351993 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YL | LL127YL | ll12 7yl | ll127yl | Wrexham | Wrecsam | Gresford STW | 4124 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333845 | 351789 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YN | LL127YN | ll12 7yn | ll127yn | Wrexham | Wrecsam | Abenbury WwTW | 4184 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333884 | 351622 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YP | LL127YP | ll12 7yp | ll127yp | Wrexham | Wrecsam | Gresford STW | 4180 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333853 | 351730 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YR | LL127YR | ll12 7yr | ll127yr | Wrexham | Wrecsam | Gresford STW | 4266 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333751 | 351668 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YS | LL127YS | ll12 7ys | ll127ys | Wrexham | Wrecsam | Gresford STW | 4237 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333713 | 351708 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YT | LL127YT | ll12 7yt | ll127yt | Wrexham | Wrecsam | Gresford STW | 4042 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334234 | 351791 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 7YW | LL127YW | ll12 7yw | ll127yw | Wrexham | Wrecsam | Gresford STW | 4099 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333829 | 351820 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AA | LL128AA | ll12 8aa | ll128aa | Wrexham | Wrecsam | Gresford STW | 3319 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334030 | 352573 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AB | LL128AB | ll12 8ab | ll128ab | Wrexham | Wrecsam | Gresford STW | 3279 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334081 | 352601 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AD | LL128AD | ll12 8ad | ll128ad | Wrexham | Wrecsam | Gresford STW | 3339 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334110 | 352532 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AE | LL128AE | ll12 8ae | ll128ae | Wrexham | Wrecsam | Gresford STW | 3244 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334125 | 352626 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AF | LL128AF | ll12 8af | ll128af | Wrexham | Wrecsam | Gresford STW | 3143 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334104 | 352735 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AG | LL128AG | ll12 8ag | ll128ag | Wrexham | Wrecsam | Gresford STW | 3206 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333987 | 352702 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AH | LL128AH | ll12 8ah | ll128ah | Wrexham | Wrecsam | Gresford STW | 3230 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334183 | 352627 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AJ | LL128AJ | ll12 8aj | ll128aj | Wrexham | Wrecsam | Gresford STW | 3416 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334048 | 352468 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AL | LL128AL | ll12 8al | ll128al | Wrexham | Wrecsam | Gresford STW | 3113 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334011 | 352792 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AN | LL128AN | ll12 8an | ll128an | Wrexham | Wrecsam | Gresford STW | 3202 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334103 | 352675 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AQ | LL128AQ | ll12 8aq | ll128aq | Wrexham | Wrecsam | Gresford STW | 3045 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333811 | 352930 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AR | LL128AR | ll12 8ar | ll128ar | Wrexham | Wrecsam | Gresford STW | 3062 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333873 | 352889 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AS | LL128AS | ll12 8as | ll128as | Wrexham | Wrecsam | Gresford STW | 3113 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334113 | 352764 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AT | LL128AT | ll12 8at | ll128at | Wrexham | Wrecsam | Gresford STW | 3159 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333791 | 352816 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AU | LL128AU | ll12 8au | ll128au | Wrexham | Wrecsam | Gresford STW | 3202 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333775 | 352776 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AW | LL128AW | ll12 8aw | ll128aw | Wrexham | Wrecsam | Gresford STW | 3010 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333902 | 352934 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8AY | LL128AY | ll12 8ay | ll128ay | Wrexham | Wrecsam | Gresford STW | 3106 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333866 | 352845 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BA | LL128BA | ll12 8ba | ll128ba | Wrexham | Wrecsam | Gresford STW | 3177 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333842 | 352778 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BB | LL128BB | ll12 8bb | ll128bb | Wrexham | Wrecsam | Gresford STW | 3184 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333952 | 352735 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BD | LL128BD | ll12 8bd | ll128bd | Wrexham | Wrecsam | Gresford STW | 3179 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333883 | 352763 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BE | LL128BE | ll12 8be | ll128be | Wrexham | Wrecsam | Gresford STW | 3286 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333930 | 352636 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BG | LL128BG | ll12 8bg | ll128bg | Wrexham | Wrecsam | Gresford STW | 3390 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333904 | 352535 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BH | LL128BH | ll12 8bh | ll128bh | Wrexham | Wrecsam | Gresford STW | 3218 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333854 | 352731 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BL | LL128BL | ll12 8bl | ll128bl | Wrexham | Wrecsam | Gresford STW | 3406 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333839 | 352538 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BN | LL128BN | ll12 8bn | ll128bn | Wrexham | Wrecsam | Gresford STW | 3414 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333878 | 352518 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BS | LL128BS | ll12 8bs | ll128bs | Wrexham | Wrecsam | Gresford STW | 3713 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334065 | 352159 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BT | LL128BT | ll12 8bt | ll128bt | Wrexham | Wrecsam | Gresford STW | 3755 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334044 | 352121 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BU | LL128BU | ll12 8bu | ll128bu | Wrexham | Wrecsam | Gresford STW | 4025 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333812 | 351901 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BW | LL128BW | ll12 8bw | ll128bw | Wrexham | Wrecsam | Gresford STW | 3276 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333781 | 352695 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8BY | LL128BY | ll12 8by | ll128by | Wrexham | Wrecsam | Gresford STW | 3826 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333940 | 352073 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DA | LL128DA | ll12 8da | ll128da | Wrexham | Wrecsam | Gresford STW | 3666 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334058 | 352209 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DD | LL128DD | ll12 8dd | ll128dd | Wrexham | Wrecsam | Gresford STW | 3695 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334138 | 352162 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DE | LL128DE | ll12 8de | ll128de | Wrexham | Wrecsam | Gresford STW | 3789 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334169 | 352060 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DF | LL128DF | ll12 8df | ll128df | Wrexham | Wrecsam | Gresford STW | 3517 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 334022 | 352371 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DG | LL128DG | ll12 8dg | ll128dg | Wrexham | Wrecsam | Gresford STW | 3697 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333904 | 352215 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DH | LL128DH | ll12 8dh | ll128dh | Wrexham | Wrecsam | Gresford STW | 3628 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333889 | 352291 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DL | LL128DL | ll12 8dl | ll128dl | Wrexham | Wrecsam | Gresford STW | 3583 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333906 | 352333 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DQ | LL128DQ | ll12 8dq | ll128dq | Wrexham | Wrecsam | Gresford STW | 3579 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333995 | 352313 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DS | LL128DS | ll12 8ds | ll128ds | Wrexham | Wrecsam | Gresford STW | 3561 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333817 | 352383 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DT | LL128DT | ll12 8dt | ll128dt | Wrexham | Wrecsam | Gresford STW | 3339 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333771 | 352632 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DU | LL128DU | ll12 8du | ll128du | Wrexham | Wrecsam | Gresford STW | 2855 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333832 | 353125 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DW | LL128DW | ll12 8dw | ll128dw | Wrexham | Wrecsam | Gresford STW | 3688 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333739 | 352274 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8DY | LL128DY | ll12 8dy | ll128dy | Wrexham | Wrecsam | Gresford STW | 3153 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333697 | 352858 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EA | LL128EA | ll12 8ea | ll128ea | Wrexham | Wrecsam | Gresford STW | 3055 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333721 | 352954 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EB | LL128EB | ll12 8eb | ll128eb | Wrexham | Wrecsam | Gresford STW | 842 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334972 | 354943 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8ED | LL128ED | ll12 8ed | ll128ed | Wrexham | Wrecsam | Gresford STW | 2998 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333719 | 353017 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EE | LL128EE | ll12 8ee | ll128ee | Wrexham | Wrecsam | Gresford STW | 2865 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333594 | 353221 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EF | LL128EF | ll12 8ef | ll128ef | Wrexham | Wrecsam | Gresford STW | 3968 | 780 | 700to900 | 1.56 | 1.14 | 0.84 | 14.54 | 7.75 | 8.57 | 333863 | 351946 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EG | LL128EG | ll12 8eg | ll128eg | Wrexham | Wrecsam | Gresford STW | 918 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335438 | 355052 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EH | LL128EH | ll12 8eh | ll128eh | Wrexham | Wrecsam | Gresford STW | 894 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335182 | 354939 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EJ | LL128EJ | ll12 8ej | ll128ej | Wrexham | Wrecsam | Gresford STW | 2709 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333643 | 353371 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EL | LL128EL | ll12 8el | ll128el | Wrexham | Wrecsam | Gresford STW | 924 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335108 | 354885 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EN | LL128EN | ll12 8en | ll128en | Wrexham | Wrecsam | Gresford STW | 834 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335086 | 354972 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EP | LL128EP | ll12 8ep | ll128ep | Wrexham | Wrecsam | Gresford STW | 825 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335181 | 355012 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EQ | LL128EQ | ll12 8eq | ll128eq | Wrexham | Wrecsam | Gresford STW | 2894 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 333462 | 353258 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8ER | LL128ER | ll12 8er | ll128er | Wrexham | Wrecsam | Gresford STW | 899 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335247 | 354960 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8ES | LL128ES | ll12 8es | ll128es | Wrexham | Wrecsam | Gresford STW | 885 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335314 | 355009 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8ET | LL128ET | ll12 8et | ll128et | Wrexham | Wrecsam | Gresford STW | 713 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334774 | 355075 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EU | LL128EU | ll12 8eu | ll128eu | Wrexham | Wrecsam | Gresford STW | 788 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334900 | 354993 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EW | LL128EW | ll12 8ew | ll128ew | Wrexham | Wrecsam | Gresford STW | 889 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335022 | 354903 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EY | LL128EY | ll12 8ey | ll128ey | Wrexham | Wrecsam | Gresford STW | 765 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335068 | 355039 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8EZ | LL128EZ | ll12 8ez | ll128ez | Wrexham | Wrecsam | Gresford STW | 2777 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333501 | 353371 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HA | LL128HA | ll12 8ha | ll128ha | Wrexham | Wrecsam | Gresford STW | 758 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335089 | 355052 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HB | LL128HB | ll12 8hb | ll128hb | Wrexham | Wrecsam | Gresford STW | 791 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335361 | 355152 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HD | LL128HD | ll12 8hd | ll128hd | Wrexham | Wrecsam | Gresford STW | 923 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335532 | 355127 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HE | LL128HE | ll12 8he | ll128he | Wrexham | Wrecsam | Gresford STW | 720 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335198 | 355134 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HF | LL128HF | ll12 8hf | ll128hf | Wrexham | Wrecsam | Gresford STW | 727 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335051 | 355074 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HG | LL128HG | ll12 8hg | ll128hg | Wrexham | Wrecsam | Gresford STW | 657 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335114 | 355166 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HH | LL128HH | ll12 8hh | ll128hh | Wrexham | Wrecsam | Gresford STW | 692 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335052 | 355110 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HL | LL128HL | ll12 8hl | ll128hl | Wrexham | Wrecsam | Gresford STW | 680 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334913 | 355101 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HN | LL128HN | ll12 8hn | ll128hn | Wrexham | Wrecsam | Gresford STW | 709 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334884 | 355071 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HP | LL128HP | ll12 8hp | ll128hp | Wrexham | Wrecsam | Gresford STW | 615 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335037 | 355186 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HR | LL128HR | ll12 8hr | ll128hr | Wrexham | Wrecsam | Gresford STW | 602 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334956 | 355183 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HS | LL128HS | ll12 8hs | ll128hs | Wrexham | Wrecsam | Gresford STW | 646 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334892 | 355134 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HT | LL128HT | ll12 8ht | ll128ht | Wrexham | Wrecsam | Gresford STW | 715 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334914 | 355066 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HU | LL128HU | ll12 8hu | ll128hu | Wrexham | Wrecsam | Gresford STW | 726 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335326 | 355207 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HW | LL128HW | ll12 8hw | ll128hw | Wrexham | Wrecsam | Gresford STW | 583 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335116 | 355247 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8HY | LL128HY | ll12 8hy | ll128hy | Wrexham | Wrecsam | Gresford STW | 847 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334892 | 354933 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JA | LL128JA | ll12 8ja | ll128ja | Wrexham | Wrecsam | Gresford STW | 3012 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334078 | 352878 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JB | LL128JB | ll12 8jb | ll128jb | Wrexham | Wrecsam | Gresford STW | 3006 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334004 | 352906 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JD | LL128JD | ll12 8jd | ll128jd | Wrexham | Wrecsam | Gresford STW | 2948 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333991 | 352970 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JE | LL128JE | ll12 8je | ll128je | Wrexham | Wrecsam | Gresford STW | 2834 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333961 | 353100 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JF | LL128JF | ll12 8jf | ll128jf | Wrexham | Wrecsam | Gresford STW | 2998 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333856 | 352963 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JG | LL128JG | ll12 8jg | ll128jg | Wrexham | Wrecsam | Gresford STW | 2919 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333822 | 353061 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JH | LL128JH | ll12 8jh | ll128jh | Wrexham | Wrecsam | Gresford STW | 3039 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334104 | 352843 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JJ | LL128JJ | ll12 8jj | ll128jj | Wrexham | Wrecsam | Gresford STW | 3028 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334194 | 352832 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JL | LL128JL | ll12 8jl | ll128jl | Wrexham | Wrecsam | Gresford STW | 2972 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334248 | 352877 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JN | LL128JN | ll12 8jn | ll128jn | Wrexham | Wrecsam | Gresford STW | 3044 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334146 | 352827 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JP | LL128JP | ll12 8jp | ll128jp | Wrexham | Wrecsam | Gresford STW | 2881 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334239 | 352972 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JQ | LL128JQ | ll12 8jq | ll128jq | Wrexham | Wrecsam | Gresford STW | 2882 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333927 | 353061 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JR | LL128JR | ll12 8jr | ll128jr | Wrexham | Wrecsam | Gresford STW | 2881 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334123 | 353001 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JS | LL128JS | ll12 8js | ll128js | Wrexham | Wrecsam | Gresford STW | 2816 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334129 | 353067 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JT | LL128JT | ll12 8jt | ll128jt | Wrexham | Wrecsam | Gresford STW | 2785 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334134 | 353098 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JU | LL128JU | ll12 8ju | ll128ju | Wrexham | Wrecsam | Gresford STW | 2855 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334204 | 353007 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JW | LL128JW | ll12 8jw | ll128jw | Wrexham | Wrecsam | Gresford STW | 2892 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334169 | 352978 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JX | LL128JX | ll12 8jx | ll128jx | Wrexham | Wrecsam | Gresford STW | 2849 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334009 | 353068 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JY | LL128JY | ll12 8jy | ll128jy | Wrexham | Wrecsam | Gresford STW | 2768 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334064 | 353136 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8JZ | LL128JZ | ll12 8jz | ll128jz | Wrexham | Wrecsam | Gresford STW | 2819 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334107 | 353070 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LA | LL128LA | ll12 8la | ll128la | Wrexham | Wrecsam | Gresford STW | 1170 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335868 | 355154 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LB | LL128LB | ll12 8lb | ll128lb | Wrexham | Wrecsam | Gresford STW | 1335 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335853 | 354866 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LD | LL128LD | ll12 8ld | ll128ld | Wrexham | Wrecsam | Gresford STW | 1423 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335900 | 354788 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LE | LL128LE | ll12 8le | ll128le | Wrexham | Wrecsam | Gresford STW | 1343 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 336138 | 355310 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LF | LL128LF | ll12 8lf | ll128lf | Wrexham | Wrecsam | Gresford STW | 1205 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335956 | 355238 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LG | LL128LG | ll12 8lg | ll128lg | Wrexham | Wrecsam | Gresford STW | 1388 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 336074 | 355073 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LH | LL128LH | ll12 8lh | ll128lh | Wrexham | Wrecsam | Gresford STW | 1549 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 336179 | 354937 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LL | LL128LL | ll12 8ll | ll128ll | Wrexham | Wrecsam | Gresford STW | 1489 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 336065 | 354879 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LN | LL128LN | ll12 8ln | ll128ln | Wrexham | Wrecsam | Gresford STW | 1472 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 336057 | 354897 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LP | LL128LP | ll12 8lp | ll128lp | Wrexham | Wrecsam | Gresford STW | 1246 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335942 | 355129 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LQ | LL128LQ | ll12 8lq | ll128lq | Wrexham | Wrecsam | Gresford STW | 2783 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333963 | 353153 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LR | LL128LR | ll12 8lr | ll128lr | Wrexham | Wrecsam | Gresford STW | 1290 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335908 | 355001 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LS | LL128LS | ll12 8ls | ll128ls | Wrexham | Wrecsam | Gresford STW | 1232 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335801 | 354963 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LT | LL128LT | ll12 8lt | ll128lt | Wrexham | Wrecsam | Gresford STW | 1232 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335870 | 355047 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LU | LL128LU | ll12 8lu | ll128lu | Wrexham | Wrecsam | Gresford STW | 1362 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335944 | 354930 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LW | LL128LW | ll12 8lw | ll128lw | Wrexham | Wrecsam | Gresford STW | 1506 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 336016 | 354792 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LX | LL128LX | ll12 8lx | ll128lx | Wrexham | Wrecsam | Gresford STW | 2353 | 776 | 700to900 | 1.55 | 1.14 | 0.83 | 14.46 | 7.71 | 8.53 | 333872 | 353655 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LY | LL128LY | ll12 8ly | ll128ly | Wrexham | Wrecsam | Gresford STW | 1405 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335794 | 354713 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8LZ | LL128LZ | ll12 8lz | ll128lz | Wrexham | Wrecsam | Gresford STW | 1366 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335837 | 354806 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NA | LL128NA | ll12 8na | ll128na | Wrexham | Wrecsam | Gresford STW | 1126 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334959 | 354657 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NB | LL128NB | ll12 8nb | ll128nb | Wrexham | Wrecsam | Gresford STW | 1104 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335014 | 354685 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8ND | LL128ND | ll12 8nd | ll128nd | Wrexham | Wrecsam | Gresford STW | 1024 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335663 | 355120 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NE | LL128NE | ll12 8ne | ll128ne | Wrexham | Wrecsam | Gresford STW | 1133 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335092 | 354667 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NF | LL128NF | ll12 8nf | ll128nf | Wrexham | Wrecsam | Gresford STW | 1200 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335147 | 354611 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NG | LL128NG | ll12 8ng | ll128ng | Wrexham | Wrecsam | Gresford STW | 1016 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334973 | 354769 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NH | LL128NH | ll12 8nh | ll128nh | Wrexham | Wrecsam | Gresford STW | 1078 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335252 | 354769 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NL | LL128NL | ll12 8nl | ll128nl | Wrexham | Wrecsam | Gresford STW | 879 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334880 | 354901 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NN | LL128NN | ll12 8nn | ll128nn | Wrexham | Wrecsam | Gresford STW | 965 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335006 | 354824 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NP | LL128NP | ll12 8np | ll128np | Wrexham | Wrecsam | Gresford STW | 1165 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335221 | 354666 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NQ | LL128NQ | ll12 8nq | ll128nq | Wrexham | Wrecsam | Gresford STW | 1178 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335328 | 354691 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NR | LL128NR | ll12 8nr | ll128nr | Wrexham | Wrecsam | Gresford STW | 1028 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335142 | 354786 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NS | LL128NS | ll12 8ns | ll128ns | Wrexham | Wrecsam | Gresford STW | 964 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335126 | 354848 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NT | LL128NT | ll12 8nt | ll128nt | Wrexham | Wrecsam | Gresford STW | 1083 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335320 | 354791 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NU | LL128NU | ll12 8nu | ll128nu | Wrexham | Wrecsam | Gresford STW | 943 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335307 | 354940 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NW | LL128NW | ll12 8nw | ll128nw | Wrexham | Wrecsam | Gresford STW | 1175 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335189 | 354647 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8NZ | LL128NZ | ll12 8nz | ll128nz | Wrexham | Wrecsam | Gresford STW | 1135 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335386 | 354764 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PA | LL128PA | ll12 8pa | ll128pa | Wrexham | Wrecsam | Gresford STW | 1012 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335446 | 354941 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PB | LL128PB | ll12 8pb | ll128pb | Wrexham | Wrecsam | Gresford STW | 1005 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335549 | 355030 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PD | LL128PD | ll12 8pd | ll128pd | Wrexham | Wrecsam | Gresford STW | 986 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335636 | 355147 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PF | LL128PF | ll12 8pf | ll128pf | Wrexham | Wrecsam | Gresford STW | 1023 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334932 | 354759 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PG | LL128PG | ll12 8pg | ll128pg | Wrexham | Wrecsam | Gresford STW | 1050 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334735 | 354740 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PH | LL128PH | ll12 8ph | ll128ph | Wrexham | Wrecsam | Gresford STW | 1023 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335627 | 355081 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PN | LL128PN | ll12 8pn | ll128pn | Wrexham | Wrecsam | Gresford STW | 1050 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335666 | 355085 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PP | LL128PP | ll12 8pp | ll128pp | Wrexham | Wrecsam | Gresford STW | 1846 | 776 | 700to900 | 1.55 | 1.14 | 0.83 | 14.46 | 7.71 | 8.53 | 334409 | 353996 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PQ | LL128PQ | ll12 8pq | ll128pq | Wrexham | Wrecsam | Gresford STW | 2743 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333568 | 353372 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PR | LL128PR | ll12 8pr | ll128pr | Wrexham | Wrecsam | Gresford STW | 1094 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334950 | 354689 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PS | LL128PS | ll12 8ps | ll128ps | Wrexham | Wrecsam | Gresford STW | 942 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334764 | 354846 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PT | LL128PT | ll12 8pt | ll128pt | Wrexham | Wrecsam | Gresford STW | 954 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334852 | 354827 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PU | LL128PU | ll12 8pu | ll128pu | Wrexham | Wrecsam | Gresford STW | 994 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334755 | 354794 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PW | LL128PW | ll12 8pw | ll128pw | Wrexham | Wrecsam | Gresford STW | 1837 | 776 | 700to900 | 1.55 | 1.14 | 0.83 | 14.46 | 7.71 | 8.53 | 334288 | 354042 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PY | LL128PY | ll12 8py | ll128py | Wrexham | Wrecsam | Gresford STW | 893 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334818 | 354889 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8PZ | LL128PZ | ll12 8pz | ll128pz | Wrexham | Wrecsam | Gresford STW | 2883 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 333508 | 353245 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RA | LL128RA | ll12 8ra | ll128ra | Wrexham | Wrecsam | Gresford STW | 918 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334779 | 354868 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RB | LL128RB | ll12 8rb | ll128rb | Wrexham | Wrecsam | Gresford STW | 881 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334737 | 354911 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RD | LL128RD | ll12 8rd | ll128rd | Wrexham | Wrecsam | Gresford STW | 864 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334724 | 354931 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RE | LL128RE | ll12 8re | ll128re | Wrexham | Wrecsam | Gresford STW | 816 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334745 | 354976 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RF | LL128RF | ll12 8rf | ll128rf | Wrexham | Wrecsam | Gresford STW | 828 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334720 | 354968 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RG | LL128RG | ll12 8rg | ll128rg | Wrexham | Wrecsam | Gresford STW | 802 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334618 | 355022 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RH | LL128RH | ll12 8rh | ll128rh | Wrexham | Wrecsam | Gresford STW | 660 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334646 | 355163 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RJ | LL128RJ | ll12 8rj | ll128rj | Wrexham | Wrecsam | Gresford STW | 771 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334624 | 355053 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RL | LL128RL | ll12 8rl | ll128rl | Wrexham | Wrecsam | Gresford STW | 818 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 334206 | 355317 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RN | LL128RN | ll12 8rn | ll128rn | Wrexham | Wrecsam | Gresford STW | 1113 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 333889 | 355275 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RP | LL128RP | ll12 8rp | ll128rp | Wrexham | Wrecsam | Gresford STW | 1230 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334610 | 354580 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RQ | LL128RQ | ll12 8rq | ll128rq | Wrexham | Wrecsam | Gresford STW | 792 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334558 | 355057 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RR | LL128RR | ll12 8rr | ll128rr | Wrexham | Wrecsam | Gresford STW | 1178 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334548 | 354650 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RS | LL128RS | ll12 8rs | ll128rs | Wrexham | Wrecsam | Gresford STW | 1203 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334514 | 354634 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RT | LL128RT | ll12 8rt | ll128rt | Wrexham | Wrecsam | Gresford STW | 1410 | 770 | 700to900 | 1.54 | 1.13 | 0.83 | 14.35 | 7.65 | 8.46 | 334108 | 354601 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RU | LL128RU | ll12 8ru | ll128ru | Wrexham | Wrecsam | Gresford STW | 2052 | 776 | 700to900 | 1.55 | 1.14 | 0.83 | 14.46 | 7.71 | 8.53 | 333587 | 354187 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RW | LL128RW | ll12 8rw | ll128rw | Wrexham | Wrecsam | Gresford STW | 1031 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334619 | 354783 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8RY | LL128RY | ll12 8ry | ll128ry | Wrexham | Wrecsam | Gresford STW | 2144 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 333327 | 354303 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SA | LL128SA | ll12 8sa | ll128sa | Wrexham | Wrecsam | Gresford STW | 2384 | 800 | 700to900 | 1.6 | 1.17 | 0.86 | 14.91 | 7.95 | 8.79 | 333156 | 354134 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SE | LL128SE | ll12 8se | ll128se | Wrexham | Wrecsam | Gresford STW | 1021 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335778 | 355294 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SF | LL128SF | ll12 8sf | ll128sf | Wrexham | Wrecsam | Gresford STW | 1080 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335790 | 355199 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SG | LL128SG | ll12 8sg | ll128sg | Wrexham | Wrecsam | Gresford STW | 960 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335651 | 355209 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SH | LL128SH | ll12 8sh | ll128sh | Wrexham | Wrecsam | Gresford STW | 1002 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335767 | 355315 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SJ | LL128SJ | ll12 8sj | ll128sj | Wrexham | Wrecsam | Gresford STW | 888 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335695 | 355429 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SL | LL128SL | ll12 8sl | ll128sl | Wrexham | Wrecsam | Gresford STW | 1108 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335847 | 355240 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SP | LL128SP | ll12 8sp | ll128sp | Wrexham | Wrecsam | Gresford STW | 1050 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335854 | 355389 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SR | LL128SR | ll12 8sr | ll128sr | Wrexham | Wrecsam | Gresford STW | 1040 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335863 | 355443 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SS | LL128SS | ll12 8ss | ll128ss | Wrexham | Wrecsam | Gresford STW | 986 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 335847 | 355589 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8ST | LL128ST | ll12 8st | ll128st | Wrexham | Wrecsam | Gresford STW | 1107 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 335966 | 355570 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SU | LL128SU | ll12 8su | ll128su | Wrexham | Wrecsam | Gresford STW | 1085 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335926 | 355495 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SW | LL128SW | ll12 8sw | ll128sw | Wrexham | Wrecsam | Gresford STW | 1178 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 335985 | 356188 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SX | LL128SX | ll12 8sx | ll128sx | Wrexham | Wrecsam | Gresford STW | 1194 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 336062 | 355948 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SY | LL128SY | ll12 8sy | ll128sy | Wrexham | Wrecsam | Gresford STW | 1180 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335985 | 355368 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8SZ | LL128SZ | ll12 8sz | ll128sz | Wrexham | Wrecsam | Gresford STW | 1228 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 336040 | 356181 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TA | LL128TA | ll12 8ta | ll128ta | Wrexham | Wrecsam | Gresford STW | 1089 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 335959 | 355927 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TB | LL128TB | ll12 8tb | ll128tb | Wrexham | Wrecsam | Gresford STW | 1095 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 335923 | 356113 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TD | LL128TD | ll12 8td | ll128td | Wrexham | Wrecsam | Gresford STW | 1313 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 336034 | 356405 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TE | LL128TE | ll12 8te | ll128te | Wrexham | Wrecsam | Gresford STW | 1142 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 336002 | 355570 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TF | LL128TF | ll12 8tf | ll128tf | Wrexham | Wrecsam | Gresford STW | 1180 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 335922 | 356332 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TG | LL128TG | ll12 8tg | ll128tg | Wrexham | Wrecsam | Gresford STW | 1125 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 335807 | 356416 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TJ | LL128TJ | ll12 8tj | ll128tj | Wrexham | Wrecsam | Gresford STW | 1103 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 335930 | 356117 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TL | LL128TL | ll12 8tl | ll128tl | Wrexham | Wrecsam | Gresford STW | 1175 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334843 | 354606 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TN | LL128TN | ll12 8tn | ll128tn | Wrexham | Wrecsam | Gresford STW | 1236 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334858 | 354545 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TP | LL128TP | ll12 8tp | ll128tp | Wrexham | Wrecsam | Gresford STW | 1284 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334892 | 354497 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TQ | LL128TQ | ll12 8tq | ll128tq | Wrexham | Wrecsam | Gresford STW | 1085 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 335949 | 355965 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TR | LL128TR | ll12 8tr | ll128tr | Wrexham | Wrecsam | Gresford STW | 1310 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334815 | 354472 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TS | LL128TS | ll12 8ts | ll128ts | Wrexham | Wrecsam | Gresford STW | 1454 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334617 | 354350 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TT | LL128TT | ll12 8tt | ll128tt | Wrexham | Wrecsam | Gresford STW | 1517 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334648 | 354281 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TU | LL128TU | ll12 8tu | ll128tu | Wrexham | Wrecsam | Gresford STW | 1490 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334589 | 354319 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TW | LL128TW | ll12 8tw | ll128tw | Wrexham | Wrecsam | Gresford STW | 1440 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334699 | 354352 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TX | LL128TX | ll12 8tx | ll128tx | Wrexham | Wrecsam | Gresford STW | 1097 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 335951 | 356015 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TY | LL128TY | ll12 8ty | ll128ty | Wrexham | Wrecsam | Gresford STW | 2316 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 334514 | 353494 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8TZ | LL128TZ | ll12 8tz | ll128tz | Wrexham | Wrecsam | Gresford STW | 1446 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334838 | 354335 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UA | LL128UA | ll12 8ua | ll128ua | Wrexham | Wrecsam | Gresford STW | 1552 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334928 | 354229 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UB | LL128UB | ll12 8ub | ll128ub | Wrexham | Wrecsam | Gresford STW | 1788 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334808 | 353994 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UD | LL128UD | ll12 8ud | ll128ud | Wrexham | Wrecsam | Gresford STW | 1312 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334885 | 354468 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UE | LL128UE | ll12 8ue | ll128ue | Wrexham | Wrecsam | Gresford STW | 1294 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334937 | 354488 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UF | LL128UF | ll12 8uf | ll128uf | Wrexham | Wrecsam | Gresford STW | 1277 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334940 | 354505 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UG | LL128UG | ll12 8ug | ll128ug | Wrexham | Wrecsam | Gresford STW | 1257 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334947 | 354525 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UH | LL128UH | ll12 8uh | ll128uh | Wrexham | Wrecsam | Gresford STW | 1229 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334951 | 354553 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UL | LL128UL | ll12 8ul | ll128ul | Wrexham | Wrecsam | Gresford STW | 1220 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334980 | 354565 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UN | LL128UN | ll12 8un | ll128un | Wrexham | Wrecsam | Gresford STW | 1195 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334986 | 354590 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UP | LL128UP | ll12 8up | ll128up | Wrexham | Wrecsam | Gresford STW | 1207 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335076 | 354589 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UR | LL128UR | ll12 8ur | ll128ur | Wrexham | Wrecsam | Gresford STW | 1295 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335177 | 354520 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8US | LL128US | ll12 8us | ll128us | Wrexham | Wrecsam | Gresford STW | 1376 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335367 | 354494 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UT | LL128UT | ll12 8ut | ll128ut | Wrexham | Wrecsam | Gresford STW | 1712 | 737 | 700to900 | 1.47 | 1.08 | 0.79 | 13.73 | 7.33 | 8.1 | 335751 | 354307 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UW | LL128UW | ll12 8uw | ll128uw | Wrexham | Wrecsam | Gresford STW | 1225 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335106 | 354576 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8UY | LL128UY | ll12 8uy | ll128uy | Wrexham | Wrecsam | Gresford STW | 1664 | 737 | 700to900 | 1.47 | 1.08 | 0.79 | 13.73 | 7.33 | 8.1 | 335590 | 354276 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8XH | LL128XH | ll12 8xh | ll128xh | Wrexham | Wrecsam | Gresford STW | 1548 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335942 | 354654 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8XJ | LL128XJ | ll12 8xj | ll128xj | Wrexham | Wrecsam | Gresford STW | 1548 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335966 | 354678 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8XL | LL128XL | ll12 8xl | ll128xl | Wrexham | Wrecsam | Gresford STW | 1373 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335772 | 354737 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8XN | LL128XN | ll12 8xn | ll128xn | Wrexham | Wrecsam | Gresford STW | 1259 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335699 | 354825 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8XQ | LL128XQ | ll12 8xq | ll128xq | Wrexham | Wrecsam | Gresford STW | 1495 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335887 | 354676 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8XR | LL128XR | ll12 8xr | ll128xr | Wrexham | Wrecsam | Gresford STW | 1319 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335712 | 354757 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8XS | LL128XS | ll12 8xs | ll128xs | Wrexham | Wrecsam | Gresford STW | 1197 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335669 | 354880 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8XT | LL128XT | ll12 8xt | ll128xt | Wrexham | Wrecsam | Gresford STW | 1238 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335728 | 354879 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8XU | LL128XU | ll12 8xu | ll128xu | Wrexham | Wrecsam | Gresford STW | 1180 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335738 | 354971 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8XY | LL128XY | ll12 8xy | ll128xy | Wrexham | Wrecsam | Gresford STW | 1265 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335656 | 354781 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YA | LL128YA | ll12 8ya | ll128ya | Wrexham | Wrecsam | Gresford STW | 1939 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 336425 | 354610 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YB | LL128YB | ll12 8yb | ll128yb | Wrexham | Wrecsam | Gresford STW | 1987 | 737 | 700to900 | 1.47 | 1.08 | 0.79 | 13.73 | 7.33 | 8.1 | 336353 | 354448 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YD | LL128YD | ll12 8yd | ll128yd | Wrexham | Wrecsam | Gresford STW | 2167 | 713 | 700to900 | 1.43 | 1.04 | 0.76 | 13.28 | 7.08 | 7.83 | 336662 | 354548 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YE | LL128YE | ll12 8ye | ll128ye | Wrexham | Wrecsam | Gresford STW | 1292 | 725 | 700to900 | 1.45 | 1.06 | 0.78 | 13.51 | 7.2 | 7.96 | 336159 | 355597 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YF | LL128YF | ll12 8yf | ll128yf | Wrexham | Wrecsam | Gresford STW | 1796 | 713 | 700to900 | 1.43 | 1.04 | 0.76 | 13.28 | 7.08 | 7.83 | 336568 | 355167 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YG | LL128YG | ll12 8yg | ll128yg | Wrexham | Wrecsam | Gresford STW | 1713 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 336149 | 354630 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YH | LL128YH | ll12 8yh | ll128yh | Wrexham | Wrecsam | Gresford STW | 758 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 334874 | 355022 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YJ | LL128YJ | ll12 8yj | ll128yj | Wrexham | Wrecsam | Gresford STW | 1152 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335621 | 354899 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YL | LL128YL | ll12 8yl | ll128yl | Wrexham | Wrecsam | Gresford STW | 1181 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335546 | 354805 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YN | LL128YN | ll12 8yn | ll128yn | Wrexham | Wrecsam | Gresford STW | 1511 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335839 | 354613 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YP | LL128YP | ll12 8yp | ll128yp | Wrexham | Wrecsam | Gresford STW | 1404 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335737 | 354669 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YQ | LL128YQ | ll12 8yq | ll128yq | Wrexham | Wrecsam | Gresford STW | 1124 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335549 | 354877 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YT | LL128YT | ll12 8yt | ll128yt | Wrexham | Wrecsam | Gresford STW | 1213 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335552 | 354771 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YU | LL128YU | ll12 8yu | ll128yu | Wrexham | Wrecsam | Gresford STW | 1251 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335530 | 354712 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YX | LL128YX | ll12 8yx | ll128yx | Wrexham | Wrecsam | Gresford STW | 1098 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335550 | 354910 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YY | LL128YY | ll12 8yy | ll128yy | Wrexham | Wrecsam | Gresford STW | 1049 | 749 | 700to900 | 1.5 | 1.1 | 0.8 | 13.96 | 7.45 | 8.23 | 335461 | 354907 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8YZ | LL128YZ | ll12 8yz | ll128yz | Wrexham | Wrecsam | Gresford STW | 1152 | 733 | 700to900 | 1.47 | 1.07 | 0.79 | 13.66 | 7.28 | 8.05 | 335664 | 354937 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 8ZJ | LL128ZJ | ll12 8zj | ll128zj | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9AA | LL129AA | ll12 9aa | ll129aa | Flintshire | Sir Y Fflint | Hope WwTW | 500 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330457 | 357604 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AB | LL129AB | ll12 9ab | ll129ab | Flintshire | Sir Y Fflint | Hope WwTW | 533 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330587 | 357560 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AD | LL129AD | ll12 9ad | ll129ad | Flintshire | Sir Y Fflint | Hope WwTW | 661 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330728 | 357452 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AE | LL129AE | ll12 9ae | ll129ae | Flintshire | Sir Y Fflint | Hope WwTW | 379 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330443 | 357733 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AF | LL129AF | ll12 9af | ll129af | Flintshire | Sir Y Fflint | Hope WwTW | 405 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330544 | 357688 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AG | LL129AG | ll12 9ag | ll129ag | Flintshire | Sir Y Fflint | Hope WwTW | 306 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330551 | 357786 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AH | LL129AH | ll12 9ah | ll129ah | Flintshire | Sir Y Fflint | Hope WwTW | 337 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330463 | 357770 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AJ | LL129AJ | ll12 9aj | ll129aj | Flintshire | Sir Y Fflint | Hope WwTW | 395 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330952 | 358161 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AL | LL129AL | ll12 9al | ll129al | Flintshire | Sir Y Fflint | Hope WwTW | 573 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330544 | 357520 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AN | LL129AN | ll12 9an | ll129an | Flintshire | Sir Y Fflint | Hope WwTW | 478 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330701 | 357635 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AP | LL129AP | ll12 9ap | ll129ap | Flintshire | Sir Y Fflint | Hope WwTW | 631 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330902 | 357560 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AQ | LL129AQ | ll12 9aq | ll129aq | Flintshire | Sir Y Fflint | Hope WwTW | 640 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330667 | 357461 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AR | LL129AR | ll12 9ar | ll129ar | Flintshire | Sir Y Fflint | Hope WwTW | 626 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330950 | 357600 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AS | LL129AS | ll12 9as | ll129as | Flintshire | Sir Y Fflint | Hope WwTW | 614 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330936 | 357605 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AT | LL129AT | ll12 9at | ll129at | Flintshire | Sir Y Fflint | Hope WwTW | 478 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330752 | 357653 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AU | LL129AU | ll12 9au | ll129au | Flintshire | Sir Y Fflint | Hope WwTW | 536 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330820 | 357622 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AW | LL129AW | ll12 9aw | ll129aw | Flintshire | Sir Y Fflint | Hope WwTW | 507 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330753 | 357622 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AX | LL129AX | ll12 9ax | ll129ax | Flintshire | Sir Y Fflint | Hope WwTW | 1567 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330792 | 356542 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AY | LL129AY | ll12 9ay | ll129ay | Flintshire | Sir Y Fflint | Hope WwTW | 723 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330991 | 357510 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9AZ | LL129AZ | ll12 9az | ll129az | Flintshire | Sir Y Fflint | Hope WwTW | 1630 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 330809 | 356481 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BA | LL129BA | ll12 9ba | ll129ba | Flintshire | Sir Y Fflint | Hope WwTW | 1011 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330936 | 357153 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BB | LL129BB | ll12 9bb | ll129bb | Flintshire | Sir Y Fflint | Hope WwTW | 1108 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330910 | 357040 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BD | LL129BD | ll12 9bd | ll129bd | Flintshire | Sir Y Fflint | Hope WwTW | 1043 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330903 | 357106 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BE | LL129BE | ll12 9be | ll129be | Flintshire | Sir Y Fflint | Hope WwTW | 1137 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330946 | 357022 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BG | LL129BG | ll12 9bg | ll129bg | Flintshire | Sir Y Fflint | Hope WwTW | 1163 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330966 | 357002 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BH | LL129BH | ll12 9bh | ll129bh | Flintshire | Sir Y Fflint | Hope WwTW | 1189 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330903 | 356953 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BL | LL129BL | ll12 9bl | ll129bl | Flintshire | Sir Y Fflint | Hope WwTW | 1182 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330938 | 356972 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BN | LL129BN | ll12 9bn | ll129bn | Flintshire | Sir Y Fflint | Hope WwTW | 1197 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330945 | 356958 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BP | LL129BP | ll12 9bp | ll129bp | Flintshire | Sir Y Fflint | Hope WwTW | 1429 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330994 | 356730 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BQ | LL129BQ | ll12 9bq | ll129bq | Flintshire | Sir Y Fflint | Hope WwTW | 1574 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 331047 | 356595 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BS | LL129BS | ll12 9bs | ll129bs | Flintshire | Sir Y Fflint | Hope WwTW | 1436 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330995 | 356723 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BT | LL129BT | ll12 9bt | ll129bt | Flintshire | Sir Y Fflint | Hope WwTW | 1281 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330869 | 356849 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BU | LL129BU | ll12 9bu | ll129bu | Flintshire | Sir Y Fflint | Hope WwTW | 1344 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330883 | 356787 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BW | LL129BW | ll12 9bw | ll129bw | Flintshire | Sir Y Fflint | Hope WwTW | 1215 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330952 | 356941 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BX | LL129BX | ll12 9bx | ll129bx | Flintshire | Sir Y Fflint | Hope WwTW | 617 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330615 | 357477 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9BY | LL129BY | ll12 9by | ll129by | Flintshire | Sir Y Fflint | Hope WwTW | 1401 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330945 | 356745 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9DB | LL129DB | ll12 9db | ll129db | Flintshire | Sir Y Fflint | Hope WwTW | 1468 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 331007 | 356693 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9DD | LL129DD | ll12 9dd | ll129dd | Flintshire | Sir Y Fflint | Hope WwTW | 1474 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330947 | 356669 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9DE | LL129DE | ll12 9de | ll129de | Flintshire | Sir Y Fflint | Hope WwTW | 1694 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331041 | 356467 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9DF | LL129DF | ll12 9df | ll129df | Flintshire | Sir Y Fflint | Hope WwTW | 1661 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 330993 | 356488 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9DG | LL129DG | ll12 9dg | ll129dg | Flintshire | Sir Y Fflint | Hope WwTW | 1336 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330842 | 356786 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9DH | LL129DH | ll12 9dh | ll129dh | Flintshire | Sir Y Fflint | Hope WwTW | 1692 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 330854 | 356426 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9DR | LL129DR | ll12 9dr | ll129dr | Flintshire | Sir Y Fflint | Hope WwTW | 641 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330662 | 357459 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9DS | LL129DS | ll12 9ds | ll129ds | Flintshire | Sir Y Fflint | Hope WwTW | 683 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330734 | 357431 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9DT | LL129DT | ll12 9dt | ll129dt | Flintshire | Sir Y Fflint | Hope WwTW | 779 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330930 | 357405 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9DU | LL129DU | ll12 9du | ll129du | Flintshire | Sir Y Fflint | Hope WwTW | 855 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330937 | 357324 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9DW | LL129DW | ll12 9dw | ll129dw | Flintshire | Sir Y Fflint | Hope WwTW | 659 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330702 | 357448 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9DY | LL129DY | ll12 9dy | ll129dy | Flintshire | Sir Y Fflint | Hope WwTW | 803 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330956 | 357392 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9EA | LL129EA | ll12 9ea | ll129ea | Flintshire | Sir Y Fflint | Hope WwTW | 825 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330999 | 357392 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9EB | LL129EB | ll12 9eb | ll129eb | Flintshire | Sir Y Fflint | Hope WwTW | 1180 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 331476 | 357345 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9ED | LL129ED | ll12 9ed | ll129ed | Flintshire | Sir Y Fflint | Hope WwTW | 1292 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 331675 | 357435 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9EE | LL129EE | ll12 9ee | ll129ee | Flintshire | Sir Y Fflint | Hope WwTW | 1014 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 331138 | 357257 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9EF | LL129EF | ll12 9ef | ll129ef | Flintshire | Sir Y Fflint | Hope WwTW | 1361 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 331739 | 357408 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9EL | LL129EL | ll12 9el | ll129el | Flintshire | Sir Y Fflint | Hope WwTW | 1471 | 810 | 700to900 | 1.62 | 1.19 | 0.87 | 15.1 | 8.05 | 8.9 | 331934 | 357560 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9EN | LL129EN | ll12 9en | ll129en | Flintshire | Sir Y Fflint | Hope WwTW | 1498 | 810 | 700to900 | 1.62 | 1.19 | 0.87 | 15.1 | 8.05 | 8.9 | 331946 | 357518 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9EP | LL129EP | ll12 9ep | ll129ep | Flintshire | Sir Y Fflint | Hope WwTW | 1647 | 810 | 700to900 | 1.62 | 1.19 | 0.87 | 15.1 | 8.05 | 8.9 | 332143 | 357628 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9ER | LL129ER | ll12 9er | ll129er | Flintshire | Sir Y Fflint | Hope WwTW | 1001 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 331205 | 357325 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9ES | LL129ES | ll12 9es | ll129es | Flintshire | Sir Y Fflint | Hope WwTW | 602 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330523 | 357492 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9ET | LL129ET | ll12 9et | ll129et | Flintshire | Sir Y Fflint | Hope WwTW | 626 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330554 | 357466 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9EU | LL129EU | ll12 9eu | ll129eu | Flintshire | Sir Y Fflint | Hope WwTW | 614 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 330489 | 357483 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9EW | LL129EW | ll12 9ew | ll129ew | Flintshire | Sir Y Fflint | Hope WwTW | 1638 | 815 | 700to900 | 1.63 | 1.19 | 0.88 | 15.19 | 8.1 | 8.95 | 332076 | 357465 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9EY | LL129EY | ll12 9ey | ll129ey | Flintshire | Sir Y Fflint | Hope WwTW | 607 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 330440 | 357498 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HA | LL129HA | ll12 9ha | ll129ha | Flintshire | Sir Y Fflint | Hope WwTW | 810 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329827 | 358430 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HB | LL129HB | ll12 9hb | ll129hb | Flintshire | Sir Y Fflint | Hope WwTW | 682 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 330055 | 358546 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HD | LL129HD | ll12 9hd | ll129hd | Flintshire | Sir Y Fflint | Hope WwTW | 1422 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 329150 | 358244 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HE | LL129HE | ll12 9he | ll129he | Flintshire | Sir Y Fflint | Llanfynydd STW | 1508 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 328709 | 357792 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HF | LL129HF | ll12 9hf | ll129hf | Flintshire | Sir Y Fflint | Hope WwTW | 1306 | 939 | 900to1200 | 1.88 | 1.38 | 1.01 | 17.5 | 9.33 | 10.32 | 329430 | 357443 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HG | LL129HG | ll12 9hg | ll129hg | Flintshire | Sir Y Fflint | Hope WwTW | 1181 | 921 | 900to1200 | 1.84 | 1.35 | 0.99 | 17.17 | 9.16 | 10.12 | 329420 | 357796 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HH | LL129HH | ll12 9hh | ll129hh | Flintshire | Sir Y Fflint | Hope WwTW | 639 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 329996 | 357798 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HL | LL129HL | ll12 9hl | ll129hl | Flintshire | Sir Y Fflint | Hope WwTW | 962 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330533 | 357131 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HN | LL129HN | ll12 9hn | ll129hn | Flintshire | Sir Y Fflint | Hope WwTW | 837 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330527 | 357256 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HP | LL129HP | ll12 9hp | ll129hp | Flintshire | Sir Y Fflint | Hope WwTW | 857 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 330488 | 357239 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HR | LL129HR | ll12 9hr | ll129hr | Flintshire | Sir Y Fflint | Hope WwTW | 716 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330518 | 357378 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HS | LL129HS | ll12 9hs | ll129hs | Flintshire | Sir Y Fflint | Hope WwTW | 977 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 330484 | 357119 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HT | LL129HT | ll12 9ht | ll129ht | Flintshire | Sir Y Fflint | Hope WwTW | 1309 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 330042 | 356892 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HU | LL129HU | ll12 9hu | ll129hu | Flintshire | Sir Y Fflint | Hope WwTW | 744 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 330390 | 357369 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9HY | LL129HY | ll12 9hy | ll129hy | Flintshire | Sir Y Fflint | Hope WwTW | 790 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 330414 | 357316 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LA | LL129LA | ll12 9la | ll129la | Flintshire | Sir Y Fflint | Hope WwTW | 685 | 839 | 700to900 | 1.68 | 1.23 | 0.9 | 15.64 | 8.34 | 9.22 | 330506 | 357410 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LB | LL129LB | ll12 9lb | ll129lb | Flintshire | Sir Y Fflint | Hope WwTW | 687 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 330340 | 357442 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LD | LL129LD | ll12 9ld | ll129ld | Flintshire | Sir Y Fflint | Hope WwTW | 597 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330348 | 357535 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LE | LL129LE | ll12 9le | ll129le | Flintshire | Sir Y Fflint | Hope WwTW | 640 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 330376 | 357480 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LF | LL129LF | ll12 9lf | ll129lf | Flintshire | Sir Y Fflint | Hope WwTW | 659 | 898 | 700to900 | 1.8 | 1.32 | 0.96 | 16.74 | 8.93 | 9.87 | 330424 | 357448 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LG | LL129LG | ll12 9lg | ll129lg | Flintshire | Sir Y Fflint | Hope WwTW | 553 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330422 | 357557 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LH | LL129LH | ll12 9lh | ll129lh | Flintshire | Sir Y Fflint | Hope WwTW | 531 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330386 | 357592 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LL | LL129LL | ll12 9ll | ll129ll | Flintshire | Sir Y Fflint | Hope WwTW | 516 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330423 | 357596 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LN | LL129LN | ll12 9ln | ll129ln | Flintshire | Sir Y Fflint | Hope WwTW | 422 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330268 | 357791 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LP | LL129LP | ll12 9lp | ll129lp | Flintshire | Sir Y Fflint | Hope WwTW | 417 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330339 | 357741 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LR | LL129LR | ll12 9lr | ll129lr | Flintshire | Sir Y Fflint | Hope WwTW | 435 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330140 | 357992 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LS | LL129LS | ll12 9ls | ll129ls | Flintshire | Sir Y Fflint | Hope WwTW | 440 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330157 | 357924 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LT | LL129LT | ll12 9lt | ll129lt | Flintshire | Sir Y Fflint | Hope WwTW | 468 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330116 | 357955 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LU | LL129LU | ll12 9lu | ll129lu | Flintshire | Sir Y Fflint | Hope WwTW | 487 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330193 | 357775 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9LW | LL129LW | ll12 9lw | ll129lw | Flintshire | Sir Y Fflint | Hope WwTW | 510 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330269 | 357676 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NB | LL129NB | ll12 9nb | ll129nb | Flintshire | Sir Y Fflint | Hope WwTW | 663 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 330977 | 358610 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9ND | LL129ND | ll12 9nd | ll129nd | Flintshire | Sir Y Fflint | Hope WwTW | 729 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 331018 | 358661 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NE | LL129NE | ll12 9ne | ll129ne | Flintshire | Sir Y Fflint | Hope WwTW | 628 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 330895 | 358625 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NF | LL129NF | ll12 9nf | ll129nf | Flintshire | Sir Y Fflint | Hope WwTW | 584 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 330959 | 358521 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NH | LL129NH | ll12 9nh | ll129nh | Flintshire | Sir Y Fflint | Hope WwTW | 590 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 331013 | 358473 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NJ | LL129NJ | ll12 9nj | ll129nj | Flintshire | Sir Y Fflint | Hope WwTW | 222 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330683 | 358279 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NL | LL129NL | ll12 9nl | ll129nl | Flintshire | Sir Y Fflint | Hope WwTW | 356 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330914 | 358035 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NP | LL129NP | ll12 9np | ll129np | Flintshire | Sir Y Fflint | Hope WwTW | 596 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 331022 | 357712 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NQ | LL129NQ | ll12 9nq | ll129nq | Flintshire | Sir Y Fflint | Hope WwTW | 696 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 330903 | 358699 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NR | LL129NR | ll12 9nr | ll129nr | Flintshire | Sir Y Fflint | Hope WwTW | 307 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330756 | 358330 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NS | LL129NS | ll12 9ns | ll129ns | Flintshire | Sir Y Fflint | Hope WwTW | 307 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330771 | 358318 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NT | LL129NT | ll12 9nt | ll129nt | Flintshire | Sir Y Fflint | Hope WwTW | 362 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330859 | 358301 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NU | LL129NU | ll12 9nu | ll129nu | Flintshire | Sir Y Fflint | Hope WwTW | 338 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330844 | 358279 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NW | LL129NW | ll12 9nw | ll129nw | Flintshire | Sir Y Fflint | Hope WwTW | 302 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330865 | 358100 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NX | LL129NX | ll12 9nx | ll129nx | Flintshire | Sir Y Fflint | Hope WwTW | 774 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 330867 | 358804 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NY | LL129NY | ll12 9ny | ll129ny | Flintshire | Sir Y Fflint | Hope WwTW | 229 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330757 | 358213 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9NZ | LL129NZ | ll12 9nz | ll129nz | Flintshire | Sir Y Fflint | Hope WwTW | 709 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 330742 | 358778 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PA | LL129PA | ll12 9pa | ll129pa | Flintshire | Sir Y Fflint | Hope WwTW | 255 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330793 | 358201 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PB | LL129PB | ll12 9pb | ll129pb | Flintshire | Sir Y Fflint | Hope WwTW | 265 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330824 | 358140 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PD | LL129PD | ll12 9pd | ll129pd | Flintshire | Sir Y Fflint | Hope WwTW | 565 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 331066 | 357835 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PE | LL129PE | ll12 9pe | ll129pe | Flintshire | Sir Y Fflint | Hope WwTW | 532 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 331083 | 357981 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PF | LL129PF | ll12 9pf | ll129pf | Flintshire | Sir Y Fflint | Hope WwTW | 584 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 331138 | 357989 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PG | LL129PG | ll12 9pg | ll129pg | Flintshire | Sir Y Fflint | Hope WwTW | 499 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 331019 | 357890 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PH | LL129PH | ll12 9ph | ll129ph | Flintshire | Sir Y Fflint | Hope WwTW | 483 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 331016 | 358259 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PJ | LL129PJ | ll12 9pj | ll129pj | Flintshire | Sir Y Fflint | Hope WwTW | 598 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 330433 | 358676 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PL | LL129PL | ll12 9pl | ll129pl | Flintshire | Sir Y Fflint | Hope WwTW | 567 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 331130 | 358077 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PN | LL129PN | ll12 9pn | ll129pn | Flintshire | Sir Y Fflint | Hope WwTW | 588 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 331150 | 358068 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PP | LL129PP | ll12 9pp | ll129pp | Flintshire | Sir Y Fflint | Hope WwTW | 820 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 331286 | 358478 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PQ | LL129PQ | ll12 9pq | ll129pq | Flintshire | Sir Y Fflint | Hope WwTW | 312 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330838 | 358239 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PR | LL129PR | ll12 9pr | ll129pr | Flintshire | Sir Y Fflint | Hope WwTW | 545 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330914 | 357675 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PS | LL129PS | ll12 9ps | ll129ps | Flintshire | Sir Y Fflint | Hope WwTW | 476 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330882 | 358445 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PT | LL129PT | ll12 9pt | ll129pt | Flintshire | Sir Y Fflint | Hope WwTW | 660 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 330741 | 358727 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PU | LL129PU | ll12 9pu | ll129pu | Flintshire | Sir Y Fflint | Hope WwTW | 1022 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 330476 | 359110 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PW | LL129PW | ll12 9pw | ll129pw | Flintshire | Sir Y Fflint | Hope WwTW | 612 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 331174 | 358128 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PX | LL129PX | ll12 9px | ll129px | Flintshire | Sir Y Fflint | Hope WwTW | 639 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 330361 | 358698 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PY | LL129PY | ll12 9py | ll129py | Flintshire | Sir Y Fflint | Hope WwTW | 410 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330838 | 358396 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9PZ | LL129PZ | ll12 9pz | ll129pz | Flintshire | Sir Y Fflint | Hope WwTW | 614 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 330461 | 358697 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9QA | LL129QA | ll12 9qa | ll129qa | Flintshire | Sir Y Fflint | Hope WwTW | 687 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 330438 | 358767 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RA | LL129RA | ll12 9ra | ll129ra | Flintshire | Sir Y Fflint | Hope WwTW | 357 | 828 | 700to900 | 1.66 | 1.21 | 0.89 | 15.43 | 8.23 | 9.1 | 330807 | 358352 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RB | LL129RB | ll12 9rb | ll129rb | Flintshire | Sir Y Fflint | Hope WwTW | 408 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330430 | 358478 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RE | LL129RE | ll12 9re | ll129re | Flintshire | Sir Y Fflint | Hope WwTW | 942 | 838 | 700to900 | 1.68 | 1.23 | 0.9 | 15.62 | 8.33 | 9.21 | 330498 | 359031 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RF | LL129RF | ll12 9rf | ll129rf | Flintshire | Sir Y Fflint | Hope WwTW | 1288 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 330855 | 359346 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RG | LL129RG | ll12 9rg | ll129rg | Flintshire | Sir Y Fflint | Hope WwTW | 936 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 330992 | 358924 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RH | LL129RH | ll12 9rh | ll129rh | Flintshire | Sir Y Fflint | Hope WwTW | 1143 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 330951 | 359167 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RJ | LL129RJ | ll12 9rj | ll129rj | Flintshire | Sir Y Fflint | Hope WwTW | 515 | 868 | 700to900 | 1.74 | 1.27 | 0.93 | 16.18 | 8.63 | 9.54 | 330210 | 358467 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RL | LL129RL | ll12 9rl | ll129rl | Flintshire | Sir Y Fflint | Hope WwTW | 1272 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 331141 | 359225 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RN | LL129RN | ll12 9rn | ll129rn | Flintshire | Sir Y Fflint | Hope WwTW | 1648 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 331438 | 359488 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RP | LL129RP | ll12 9rp | ll129rp | Flintshire | Sir Y Fflint | Hope WwTW | 1409 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 331365 | 359250 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RQ | LL129RQ | ll12 9rq | ll129rq | Flintshire | Sir Y Fflint | Hope WwTW | 1091 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 330938 | 359116 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RR | LL129RR | ll12 9rr | ll129rr | Flintshire | Sir Y Fflint | Hope WwTW | 1890 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 331893 | 359434 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RS | LL129RS | ll12 9rs | ll129rs | Flintshire | Sir Y Fflint | Hope WwTW | 1860 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 331824 | 359458 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RT | LL129RT | ll12 9rt | ll129rt | Flintshire | Sir Y Fflint | Hope WwTW | 1701 | 803 | 700to900 | 1.61 | 1.18 | 0.86 | 14.97 | 7.98 | 8.82 | 332175 | 358633 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RU | LL129RU | ll12 9ru | ll129ru | Flintshire | Sir Y Fflint | Hope WwTW | 1413 | 810 | 700to900 | 1.62 | 1.19 | 0.87 | 15.1 | 8.05 | 8.9 | 331961 | 357891 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RW | LL129RW | ll12 9rw | ll129rw | Flintshire | Sir Y Fflint | Hope WwTW | 1611 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 331153 | 359591 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9RY | LL129RY | ll12 9ry | ll129ry | Flintshire | Sir Y Fflint | Hope WwTW | 1541 | 810 | 700to900 | 1.62 | 1.19 | 0.87 | 15.1 | 8.05 | 8.9 | 332081 | 357828 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9SA | LL129SA | ll12 9sa | ll129sa | Flintshire | Sir Y Fflint | Hope WwTW | 1524 | 810 | 700to900 | 1.62 | 1.19 | 0.87 | 15.1 | 8.05 | 8.9 | 332064 | 357830 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9SB | LL129SB | ll12 9sb | ll129sb | Flintshire | Sir Y Fflint | Hope WwTW | 1362 | 810 | 700to900 | 1.62 | 1.19 | 0.87 | 15.1 | 8.05 | 8.9 | 331843 | 357628 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9SD | LL129SD | ll12 9sd | ll129sd | Flintshire | Sir Y Fflint | Hope WwTW | 1013 | 810 | 700to900 | 1.62 | 1.19 | 0.87 | 15.1 | 8.05 | 8.9 | 331575 | 358126 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9SE | LL129SE | ll12 9se | ll129se | Flintshire | Sir Y Fflint | Hope WwTW | 564 | 824 | 700to900 | 1.65 | 1.21 | 0.88 | 15.36 | 8.19 | 9.05 | 330898 | 358545 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9SL | LL129SL | ll12 9sl | ll129sl | Wrexham | Wrecsam | Hope WwTW | 2736 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 331074 | 355405 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9SN | LL129SN | ll12 9sn | ll129sn | Wrexham | Wrecsam | Hope WwTW | 2877 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 331154 | 355277 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9SP | LL129SP | ll12 9sp | ll129sp | Wrexham | Wrecsam | Hope WwTW | 2966 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 331124 | 355181 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9SR | LL129SR | ll12 9sr | ll129sr | Wrexham | Wrecsam | Hope WwTW | 2794 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 331043 | 355341 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9SS | LL129SS | ll12 9ss | ll129ss | Wrexham | Wrecsam | Hope WwTW | 2865 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 331145 | 355288 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9ST | LL129ST | ll12 9st | ll129st | Wrexham | Wrecsam | Hope WwTW | 2858 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 330916 | 355257 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9SU | LL129SU | ll12 9su | ll129su | Wrexham | Wrecsam | Hope WwTW | 3091 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 330686 | 355004 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9SW | LL129SW | ll12 9sw | ll129sw | Wrexham | Wrecsam | Hope WwTW | 2884 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 331124 | 355264 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9SY | LL129SY | ll12 9sy | ll129sy | Wrexham | Wrecsam | Hope WwTW | 3180 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 330692 | 354916 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9TA | LL129TA | ll12 9ta | ll129ta | Wrexham | Wrecsam | Hope WwTW | 3358 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 330704 | 354738 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9TB | LL129TB | ll12 9tb | ll129tb | Wrexham | Wrecsam | Hope WwTW | 3354 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 330551 | 354739 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9TD | LL129TD | ll12 9td | ll129td | Wrexham | Wrecsam | Hope WwTW | 3153 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 330590 | 354940 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9TE | LL129TE | ll12 9te | ll129te | Wrexham | Wrecsam | Hope WwTW | 3250 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330380 | 354848 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9TF | LL129TF | ll12 9tf | ll129tf | Wrexham | Wrecsam | Llanfynydd STW | 3348 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330283 | 354722 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9TG | LL129TG | ll12 9tg | ll129tg | Wrexham | Wrecsam | Llanfynydd STW | 3233 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330124 | 354706 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9TH | LL129TH | ll12 9th | ll129th | Wrexham | Wrecsam | Llanfynydd STW | 3061 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330080 | 354930 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9TN | LL129TN | ll12 9tn | ll129tn | Flintshire | Sir Y Fflint | Llanfynydd STW | 2865 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 329987 | 355138 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9TP | LL129TP | ll12 9tp | ll129tp | Wrexham | Wrecsam | Hope WwTW | 2962 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330439 | 355134 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9TQ | LL129TQ | ll12 9tq | ll129tq | Flintshire | Sir Y Fflint | Hope WwTW | 2111 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 330404 | 355988 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9TR | LL129TR | ll12 9tr | ll129tr | Flintshire | Sir Y Fflint | Hope WwTW | 2772 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330279 | 355336 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9TS | LL129TS | ll12 9ts | ll129ts | Flintshire | Sir Y Fflint | Hope WwTW | 2055 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 330907 | 356067 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9TU | LL129TU | ll12 9tu | ll129tu | Flintshire | Sir Y Fflint | Hope WwTW | 2456 | 906 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.89 | 9.01 | 9.95 | 330290 | 355652 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9TW | LL129TW | ll12 9tw | ll129tw | Wrexham | Wrecsam | Hope WwTW | 2877 | 905 | 900to1200 | 1.81 | 1.33 | 0.97 | 16.87 | 9 | 9.94 | 330341 | 355225 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9UB | LL129UB | ll12 9ub | ll129ub | Flintshire | Sir Y Fflint | Hope WwTW | 2053 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331137 | 356122 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9UD | LL129UD | ll12 9ud | ll129ud | Flintshire | Sir Y Fflint | Hope WwTW | 2073 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331175 | 356112 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9UE | LL129UE | ll12 9ue | ll129ue | Flintshire | Sir Y Fflint | Hope WwTW | 1991 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331217 | 356212 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9UF | LL129UF | ll12 9uf | ll129uf | Wrexham | Wrecsam | Hope WwTW | 2178 | 820 | 700to900 | 1.64 | 1.2 | 0.88 | 15.28 | 8.15 | 9.01 | 331553 | 356153 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9UG | LL129UG | ll12 9ug | ll129ug | Wrexham | Wrecsam | Hope WwTW | 2487 | 820 | 700to900 | 1.64 | 1.2 | 0.88 | 15.28 | 8.15 | 9.01 | 331655 | 355858 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9UH | LL129UH | ll12 9uh | ll129uh | Wrexham | Wrecsam | Hope WwTW | 2307 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331375 | 355933 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9UJ | LL129UJ | ll12 9uj | ll129uj | Flintshire | Sir Y Fflint | Hope WwTW | 2198 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331223 | 355996 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9UL | LL129UL | ll12 9ul | ll129ul | Flintshire | Sir Y Fflint | Hope WwTW | 1835 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331031 | 356318 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9UP | LL129UP | ll12 9up | ll129up | Flintshire | Sir Y Fflint | Hope WwTW | 2340 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331240 | 355853 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9UR | LL129UR | ll12 9ur | ll129ur | Wrexham | Wrecsam | Hope WwTW | 2607 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331215 | 355569 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9US | LL129US | ll12 9us | ll129us | Wrexham | Wrecsam | Hope WwTW | 2898 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 331293 | 355288 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9UT | LL129UT | ll12 9ut | ll129ut | Flintshire | Sir Y Fflint | Hope WwTW | 2007 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331110 | 356162 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9UU | LL129UU | ll12 9uu | ll129uu | Flintshire | Sir Y Fflint | Hope WwTW | 1981 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331103 | 356187 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9UW | LL129UW | ll12 9uw | ll129uw | Flintshire | Sir Y Fflint | Hope WwTW | 2094 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331109 | 356071 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9UY | LL129UY | ll12 9uy | ll129uy | Flintshire | Sir Y Fflint | Hope WwTW | 1983 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 330905 | 356139 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9YA | LL129YA | ll12 9ya | ll129ya | Flintshire | Sir Y Fflint | Hope WwTW | 1919 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 330943 | 356212 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9YB | LL129YB | ll12 9yb | ll129yb | Flintshire | Sir Y Fflint | Hope WwTW | 1759 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 330887 | 356364 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9YD | LL129YD | ll12 9yd | ll129yd | Flintshire | Sir Y Fflint | Hope WwTW | 1805 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 330914 | 356322 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9YE | LL129YE | ll12 9ye | ll129ye | Flintshire | Sir Y Fflint | Hope WwTW | 1923 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 330834 | 356189 | Flintshire LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Sir y Fflint | Flintshire County Council
LL12 9YF | LL129YF | ll12 9yf | ll129yf | Wrexham | Wrecsam | Gresford STW | 3135 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331800 | 355202 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9YG | LL129YG | ll12 9yg | ll129yg | Wrexham | Wrecsam | Gresford STW | 3176 | 823 | 700to900 | 1.65 | 1.21 | 0.88 | 15.34 | 8.18 | 9.04 | 331780 | 355096 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9YL | LL129YL | ll12 9yl | ll129yl | Wrexham | Wrecsam | Hope WwTW | 2664 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331189 | 355504 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9YN | LL129YN | ll12 9yn | ll129yn | Wrexham | Wrecsam | Hope WwTW | 2547 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331131 | 355610 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9YR | LL129YR | ll12 9yr | ll129yr | Wrexham | Wrecsam | Hope WwTW | 2432 | 847 | 700to900 | 1.7 | 1.24 | 0.91 | 15.79 | 8.42 | 9.31 | 331158 | 355735 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9YT | LL129YT | ll12 9yt | ll129yt | Wrexham | Wrecsam | Hope WwTW | 2910 | 859 | 700to900 | 1.72 | 1.26 | 0.92 | 16.01 | 8.54 | 9.44 | 331255 | 355266 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9ZA | LL129ZA | ll12 9za | ll129za | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL12 9ZY | LL129ZY | ll12 9zy | ll129zy | Wrexham | Wrecsam | Abenbury WwTW | 4158 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333056 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AA | LL130AA | ll13 0aa | ll130aa | Wrexham | Wrecsam | Bangor On Dee STW | 634 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339011 | 345637 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AB | LL130AB | ll13 0ab | ll130ab | Wrexham | Wrecsam | Bangor On Dee STW | 291 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 339537 | 345751 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AD | LL130AD | ll13 0ad | ll130ad | Wrexham | Wrecsam | Bangor On Dee STW | 76 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 339573 | 346020 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AE | LL130AE | ll13 0ae | ll130ae | Wrexham | Wrecsam | Worthenbury STW | 239 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 341960 | 346093 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AF | LL130AF | ll13 0af | ll130af | Wrexham | Wrecsam | Bangor On Dee STW | 907 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 338893 | 345366 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AG | LL130AG | ll13 0ag | ll130ag | Wrexham | Wrecsam | Bangor On Dee STW | 505 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 339971 | 345858 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AH | LL130AH | ll13 0ah | ll130ah | Wrexham | Wrecsam | Bangor On Dee STW | 1356 | 668 | 600to700 | 1.33 | 0.97 | 0.71 | 12.41 | 6.62 | 7.32 | 340570 | 345208 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AJ | LL130AJ | ll13 0aj | ll130aj | Wrexham | Wrecsam | Abenbury WwTW | 1177 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 335433 | 348046 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AL | LL130AL | ll13 0al | ll130al | Wrexham | Wrecsam | Worthenbury STW | 1107 | 668 | 600to700 | 1.33 | 0.97 | 0.71 | 12.41 | 6.62 | 7.32 | 341330 | 345105 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AN | LL130AN | ll13 0an | ll130an | Wrexham | Wrecsam | Worthenbury STW | 830 | 669 | 600to700 | 1.33 | 0.98 | 0.72 | 12.43 | 6.63 | 7.33 | 341777 | 345136 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AP | LL130AP | ll13 0ap | ll130ap | Wrexham | Wrecsam | Worthenbury STW | 153 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 342253 | 345911 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AQ | LL130AQ | ll13 0aq | ll130aq | Wrexham | Wrecsam | Bangor On Dee STW | 716 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339031 | 345499 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AR | LL130AR | ll13 0ar | ll130ar | Wrexham | Wrecsam | Worthenbury STW | 223 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 342056 | 346119 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AS | LL130AS | ll13 0as | ll130as | Wrexham | Wrecsam | Worthenbury STW | 349 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 342202 | 346234 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AT | LL130AT | ll13 0at | ll130at | Wrexham | Wrecsam | Bangor On Dee STW | 664 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 338962 | 345651 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AU | LL130AU | ll13 0au | ll130au | Wrexham | Wrecsam | Bangor On Dee STW | 760 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 338949 | 345517 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AW | LL130AW | ll13 0aw | ll130aw | Wrexham | Wrecsam | Worthenbury STW | 411 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 341900 | 346259 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AX | LL130AX | ll13 0ax | ll130ax | Wrexham | Wrecsam | Bangor On Dee STW | 523 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339084 | 345723 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AY | LL130AY | ll13 0ay | ll130ay | Wrexham | Wrecsam | Bangor On Dee STW | 754 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339081 | 345414 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0AZ | LL130AZ | ll13 0az | ll130az | Wrexham | Wrecsam | Worthenbury STW | 257 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 342073 | 346155 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BA | LL130BA | ll13 0ba | ll130ba | Wrexham | Wrecsam | Bangor On Dee STW | 822 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339105 | 345320 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BB | LL130BB | ll13 0bb | ll130bb | Wrexham | Wrecsam | Bangor On Dee STW | 772 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339236 | 345315 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BD | LL130BD | ll13 0bd | ll130bd | Wrexham | Wrecsam | Bangor On Dee STW | 1303 | 671 | 600to700 | 1.34 | 0.98 | 0.72 | 12.47 | 6.65 | 7.35 | 340024 | 344848 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BE | LL130BE | ll13 0be | ll130be | Wrexham | Wrecsam | Worthenbury STW | 1767 | 668 | 600to700 | 1.33 | 0.97 | 0.71 | 12.41 | 6.62 | 7.32 | 340742 | 344771 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BF | LL130BF | ll13 0bf | ll130bf | Wrexham | Wrecsam | Worthenbury STW | 315 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 342006 | 346201 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BG | LL130BG | ll13 0bg | ll130bg | Wrexham | Wrecsam | Worthenbury STW | 1769 | 665 | 600to700 | 1.33 | 0.97 | 0.71 | 12.35 | 6.59 | 7.28 | 341404 | 344274 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BH | LL130BH | ll13 0bh | ll130bh | Wrexham | Wrecsam | Worthenbury STW | 2446 | 665 | 600to700 | 1.33 | 0.97 | 0.71 | 12.35 | 6.59 | 7.28 | 340822 | 343816 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BJ | LL130BJ | ll13 0bj | ll130bj | Wrexham | Wrecsam | Worthenbury STW | 109 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 342168 | 345985 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BL | LL130BL | ll13 0bl | ll130bl | Wrexham | Wrecsam | Worthenbury STW | 2557 | 669 | 600to700 | 1.33 | 0.98 | 0.72 | 12.43 | 6.63 | 7.33 | 342025 | 343345 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BN | LL130BN | ll13 0bn | ll130bn | Wrexham | Wrecsam | Penley STW | 2685 | 669 | 600to700 | 1.33 | 0.98 | 0.72 | 12.43 | 6.63 | 7.33 | 341950 | 343103 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BP | LL130BP | ll13 0bp | ll130bp | Wrexham | Wrecsam | Penley STW | 1891 | 675 | 600to700 | 1.35 | 0.99 | 0.72 | 12.55 | 6.69 | 7.4 | 342588 | 341992 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BQ | LL130BQ | ll13 0bq | ll130bq | Wrexham | Wrecsam | Bangor On Dee STW | 729 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339304 | 345338 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BS | LL130BS | ll13 0bs | ll130bs | Wrexham | Wrecsam | Bangor On Dee STW | 761 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 338983 | 345482 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BT | LL130BT | ll13 0bt | ll130bt | Wrexham | Wrecsam | Bangor On Dee STW | 444 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339176 | 345736 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BU | LL130BU | ll13 0bu | ll130bu | Wrexham | Wrecsam | Bangor On Dee STW | 819 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 338894 | 345489 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BW | LL130BW | ll13 0bw | ll130bw | Wrexham | Wrecsam | Penley STW | 2449 | 676 | 600to700 | 1.35 | 0.99 | 0.72 | 12.57 | 6.7 | 7.41 | 342802 | 342521 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BX | LL130BX | ll13 0bx | ll130bx | Wrexham | Wrecsam | Worthenbury STW | 1802 | 665 | 600to700 | 1.33 | 0.97 | 0.71 | 12.35 | 6.59 | 7.28 | 341345 | 344264 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BY | LL130BY | ll13 0by | ll130by | Wrexham | Wrecsam | Bangor On Dee STW | 829 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 338978 | 345397 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0BZ | LL130BZ | ll13 0bz | ll130bz | Wrexham | Wrecsam | Bangor On Dee STW | 568 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339371 | 345487 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DA | LL130DA | ll13 0da | ll130da | Wrexham | Wrecsam | Bangor On Dee STW | 1770 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 338574 | 344532 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DB | LL130DB | ll13 0db | ll130db | Wrexham | Wrecsam | Bangor On Dee STW | 1702 | 672 | 600to700 | 1.34 | 0.98 | 0.72 | 12.49 | 6.66 | 7.36 | 339274 | 344354 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DD | LL130DD | ll13 0dd | ll130dd | Wrexham | Wrecsam | Erbistock STW | 1497 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 335420 | 343526 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DE | LL130DE | ll13 0de | ll130de | Wrexham | Wrecsam | Erbistock STW | 966 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 334950 | 342844 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DF | LL130DF | ll13 0df | ll130df | Wrexham | Wrecsam | Erbistock STW | 1402 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 334345 | 342866 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DG | LL130DG | ll13 0dg | ll130dg | Wrexham | Wrecsam | Erbistock STW | 1862 | 753 | 700to900 | 1.51 | 1.1 | 0.81 | 14.04 | 7.49 | 8.27 | 333710 | 342635 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DH | LL130DH | ll13 0dh | ll130dh | Wrexham | Wrecsam | Erbistock STW | 570 | 738 | 700to900 | 1.48 | 1.08 | 0.79 | 13.75 | 7.34 | 8.11 | 335058 | 341637 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DJ | LL130DJ | ll13 0dj | ll130dj | Wrexham | Wrecsam | Bangor On Dee STW | 1566 | 672 | 600to700 | 1.34 | 0.98 | 0.72 | 12.49 | 6.66 | 7.36 | 339269 | 344492 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DL | LL130DL | ll13 0dl | ll130dl | Wrexham | Wrecsam | Erbistock STW | 509 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 335520 | 341524 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DN | LL130DN | ll13 0dn | ll130dn | Wrexham | Wrecsam | Erbistock STW | 329 | 738 | 700to900 | 1.48 | 1.08 | 0.79 | 13.75 | 7.34 | 8.11 | 335434 | 341703 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DP | LL130DP | ll13 0dp | ll130dp | Wrexham | Wrecsam | Bangor On Dee STW | 885 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 338974 | 345329 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DQ | LL130DQ | ll13 0dq | ll130dq | Wrexham | Wrecsam | Overton WwTW | 916 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337467 | 341944 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DR | LL130DR | ll13 0dr | ll130dr | Wrexham | Wrecsam | Erbistock STW | 696 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335382 | 342720 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DS | LL130DS | ll13 0ds | ll130ds | Wrexham | Wrecsam | Erbistock STW | 827 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 335658 | 342835 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DT | LL130DT | ll13 0dt | ll130dt | Wrexham | Wrecsam | Overton WwTW | 742 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337296 | 341903 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DU | LL130DU | ll13 0du | ll130du | Wrexham | Wrecsam | Overton WwTW | 782 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337304 | 341975 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DW | LL130DW | ll13 0dw | ll130dw | Wrexham | Wrecsam | Erbistock STW | 237 | 738 | 700to900 | 1.48 | 1.08 | 0.79 | 13.75 | 7.34 | 8.11 | 335236 | 341991 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DX | LL130DX | ll13 0dx | ll130dx | Wrexham | Wrecsam | Overton WwTW | 734 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337349 | 341677 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DY | LL130DY | ll13 0dy | ll130dy | Wrexham | Wrecsam | Overton WwTW | 665 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337168 | 341973 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0DZ | LL130DZ | ll13 0dz | ll130dz | Wrexham | Wrecsam | Bangor On Dee STW | 901 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339159 | 345206 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EA | LL130EA | ll13 0ea | ll130ea | Wrexham | Wrecsam | Overton WwTW | 645 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337189 | 341901 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EB | LL130EB | ll13 0eb | ll130eb | Wrexham | Wrecsam | Overton WwTW | 668 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337241 | 341842 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0ED | LL130ED | ll13 0ed | ll130ed | Wrexham | Wrecsam | Overton WwTW | 661 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337261 | 341758 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EE | LL130EE | ll13 0ee | ll130ee | Wrexham | Wrecsam | Overton WwTW | 704 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337315 | 341707 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EF | LL130EF | ll13 0ef | ll130ef | Wrexham | Wrecsam | Overton WwTW | 835 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337450 | 341681 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EG | LL130EG | ll13 0eg | ll130eg | Wrexham | Wrecsam | Overton WwTW | 712 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337328 | 341527 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EH | LL130EH | ll13 0eh | ll130eh | Wrexham | Wrecsam | Overton WwTW | 738 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337357 | 341556 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EJ | LL130EJ | ll13 0ej | ll130ej | Wrexham | Wrecsam | Overton WwTW | 710 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337328 | 341648 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EL | LL130EL | ll13 0el | ll130el | Wrexham | Wrecsam | Overton WwTW | 683 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337303 | 341591 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EN | LL130EN | ll13 0en | ll130en | Wrexham | Wrecsam | Overton WwTW | 782 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337385 | 341759 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EP | LL130EP | ll13 0ep | ll130ep | Wrexham | Wrecsam | Overton WwTW | 859 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337443 | 341842 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EQ | LL130EQ | ll13 0eq | ll130eq | Wrexham | Wrecsam | Overton WwTW | 982 | 692 | 600to700 | 1.38 | 1.01 | 0.74 | 12.88 | 6.87 | 7.59 | 337571 | 341839 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0ER | LL130ER | ll13 0er | ll130er | Wrexham | Wrecsam | Overton WwTW | 939 | 692 | 600to700 | 1.38 | 1.01 | 0.74 | 12.88 | 6.87 | 7.59 | 337518 | 341871 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0ES | LL130ES | ll13 0es | ll130es | Wrexham | Wrecsam | Overton WwTW | 871 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337411 | 341961 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0ET | LL130ET | ll13 0et | ll130et | Wrexham | Wrecsam | Overton WwTW | 935 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337445 | 342037 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EU | LL130EU | ll13 0eu | ll130eu | Wrexham | Wrecsam | Overton WwTW | 903 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337415 | 342025 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EW | LL130EW | ll13 0ew | ll130ew | Wrexham | Wrecsam | Overton WwTW | 854 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337423 | 341888 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EX | LL130EX | ll13 0ex | ll130ex | Wrexham | Wrecsam | Overton WwTW | 846 | 697 | 600to700 | 1.39 | 1.02 | 0.75 | 12.97 | 6.92 | 7.65 | 337445 | 341413 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EY | LL130EY | ll13 0ey | ll130ey | Wrexham | Wrecsam | Overton WwTW | 865 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337334 | 342085 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0EZ | LL130EZ | ll13 0ez | ll130ez | Wrexham | Wrecsam | Overton WwTW | 849 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337467 | 341652 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0FA | LL130FA | ll13 0fa | ll130fa | Wrexham | Wrecsam | Overton WwTW | 793 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337371 | 341851 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0FB | LL130FB | ll13 0fb | ll130fb | Wrexham | Wrecsam | Overton WwTW | 643 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337239 | 341771 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0FD | LL130FD | ll13 0fd | ll130fd | Wrexham | Wrecsam | Worthenbury STW | 123 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 342212 | 345950 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0FE | LL130FE | ll13 0fe | ll130fe | Wrexham | Wrecsam | Erbistock STW | 4799 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332288 | 345620 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0FF | LL130FF | ll13 0ff | ll130ff | Wrexham | Wrecsam | Overton WwTW | 1064 | 692 | 600to700 | 1.38 | 1.01 | 0.74 | 12.88 | 6.87 | 7.59 | 337680 | 341685 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0FG | LL130FG | ll13 0fg | ll130fg | Wrexham | Wrecsam | Overton WwTW | 731 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337272 | 341928 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0FJ | LL130FJ | ll13 0fj | ll130fj | Wrexham | Wrecsam | Penley STW | 938 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341789 | 339575 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0FL | LL130FL | ll13 0fl | ll130fl | Wrexham | Wrecsam | Bangor On Dee STW | 2767 | 672 | 600to700 | 1.34 | 0.98 | 0.72 | 12.49 | 6.66 | 7.36 | 340386 | 343420 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0GA | LL130GA | ll13 0ga | ll130ga | Wrexham | Wrecsam | Worthenbury STW | 234 | 666 | 600to700 | 1.33 | 0.97 | 0.71 | 12.37 | 6.6 | 7.29 | 341998 | 346110 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0GB | LL130GB | ll13 0gb | ll130gb | Wrexham | Wrecsam | Penley STW | 518 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341685 | 339985 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HA | LL130HA | ll13 0ha | ll130ha | Wrexham | Wrecsam | Overton WwTW | 932 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337378 | 342138 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HB | LL130HB | ll13 0hb | ll130hb | Wrexham | Wrecsam | Overton WwTW | 900 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337402 | 342042 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HD | LL130HD | ll13 0hd | ll130hd | Wrexham | Wrecsam | Bangor On Dee STW | 779 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 338902 | 345541 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HE | LL130HE | ll13 0he | ll130he | Wrexham | Wrecsam | Overton WwTW | 1027 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337466 | 342179 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HF | LL130HF | ll13 0hf | ll130hf | Wrexham | Wrecsam | Overton WwTW | 563 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 336794 | 342132 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HG | LL130HG | ll13 0hg | ll130hg | Wrexham | Wrecsam | Erbistock STW | 924 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 336240 | 342541 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HH | LL130HH | ll13 0hh | ll130hh | Wrexham | Wrecsam | Overton WwTW | 1229 | 699 | 600to700 | 1.4 | 1.02 | 0.75 | 13.01 | 6.94 | 7.67 | 337450 | 342503 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HJ | LL130HJ | ll13 0hj | ll130hj | Wrexham | Wrecsam | Overton WwTW | 1038 | 692 | 600to700 | 1.38 | 1.01 | 0.74 | 12.88 | 6.87 | 7.59 | 337541 | 342074 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HL | LL130HL | ll13 0hl | ll130hl | Wrexham | Wrecsam | Overton WwTW | 1427 | 692 | 600to700 | 1.38 | 1.01 | 0.74 | 12.88 | 6.87 | 7.59 | 337841 | 342334 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HN | LL130HN | ll13 0hn | ll130hn | Wrexham | Wrecsam | Overton WwTW | 2451 | 674 | 600to700 | 1.34 | 0.98 | 0.72 | 12.53 | 6.68 | 7.39 | 338529 | 343133 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HP | LL130HP | ll13 0hp | ll130hp | Wrexham | Wrecsam | Overton WwTW | 2226 | 674 | 600to700 | 1.34 | 0.98 | 0.72 | 12.53 | 6.68 | 7.39 | 338559 | 342688 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HR | LL130HR | ll13 0hr | ll130hr | Wrexham | Wrecsam | Penley STW | 2314 | 674 | 600to700 | 1.34 | 0.98 | 0.72 | 12.53 | 6.68 | 7.39 | 339824 | 342075 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HS | LL130HS | ll13 0hs | ll130hs | Wrexham | Wrecsam | Penley STW | 2388 | 687 | 600to700 | 1.37 | 1 | 0.74 | 12.78 | 6.82 | 7.53 | 339099 | 340627 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HT | LL130HT | ll13 0ht | ll130ht | Wrexham | Wrecsam | Overton WwTW | 2162 | 687 | 600to700 | 1.37 | 1 | 0.74 | 12.78 | 6.82 | 7.53 | 338575 | 340676 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HU | LL130HU | ll13 0hu | ll130hu | Wrexham | Wrecsam | Overton WwTW | 2225 | 687 | 600to700 | 1.37 | 1 | 0.74 | 12.78 | 6.82 | 7.53 | 338706 | 340824 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HW | LL130HW | ll13 0hw | ll130hw | Wrexham | Wrecsam | Overton WwTW | 2451 | 679 | 600to700 | 1.35 | 0.99 | 0.73 | 12.63 | 6.73 | 7.44 | 338994 | 342204 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0HY | LL130HY | ll13 0hy | ll130hy | Wrexham | Wrecsam | Overton WwTW | 2286 | 687 | 600to700 | 1.37 | 1 | 0.74 | 12.78 | 6.82 | 7.53 | 338806 | 340930 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JA | LL130JA | ll13 0ja | ll130ja | Wrexham | Wrecsam | Bangor On Dee STW | 607 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339165 | 345534 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JB | LL130JB | ll13 0jb | ll130jb | Wrexham | Wrecsam | Bangor On Dee STW | 486 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339227 | 345638 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JD | LL130JD | ll13 0jd | ll130jd | Wrexham | Wrecsam | Bangor On Dee STW | 543 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339294 | 345538 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JE | LL130JE | ll13 0je | ll130je | Wrexham | Wrecsam | Bangor On Dee STW | 440 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339360 | 345623 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JF | LL130JF | ll13 0jf | ll130jf | Wrexham | Wrecsam | Bangor On Dee STW | 589 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339137 | 345577 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JG | LL130JG | ll13 0jg | ll130jg | Wrexham | Wrecsam | Bangor On Dee STW | 464 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339293 | 345625 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JH | LL130JH | ll13 0jh | ll130jh | Wrexham | Wrecsam | Abenbury WwTW | 1871 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 334902 | 349280 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JJ | LL130JJ | ll13 0jj | ll130jj | Wrexham | Wrecsam | Abenbury WwTW | 1738 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335057 | 349285 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JL | LL130JL | ll13 0jl | ll130jl | Wrexham | Wrecsam | Abenbury WwTW | 1870 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 334961 | 349381 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JN | LL130JN | ll13 0jn | ll130jn | Wrexham | Wrecsam | Penley STW | 1088 | 682 | 600to700 | 1.36 | 1 | 0.73 | 12.68 | 6.76 | 7.48 | 341475 | 339372 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JP | LL130JP | ll13 0jp | ll130jp | Wrexham | Wrecsam | Penley STW | 484 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341742 | 340053 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JQ | LL130JQ | ll13 0jq | ll130jq | Wrexham | Wrecsam | Bangor On Dee STW | 696 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 339066 | 345496 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JR | LL130JR | ll13 0jr | ll130jr | Wrexham | Wrecsam | Penley STW | 1190 | 682 | 600to700 | 1.36 | 1 | 0.73 | 12.68 | 6.76 | 7.48 | 341477 | 339270 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JS | LL130JS | ll13 0js | ll130js | Wrexham | Wrecsam | Penley STW | 535 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341737 | 339991 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JT | LL130JT | ll13 0jt | ll130jt | Wrexham | Wrecsam | Penley STW | 413 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341639 | 340079 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JU | LL130JU | ll13 0ju | ll130ju | Wrexham | Wrecsam | Penley STW | 851 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341947 | 339749 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JW | LL130JW | ll13 0jw | ll130jw | Wrexham | Wrecsam | Penley STW | 1128 | 682 | 600to700 | 1.36 | 1 | 0.73 | 12.68 | 6.76 | 7.48 | 341466 | 339332 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JX | LL130JX | ll13 0jx | ll130jx | Wrexham | Wrecsam | Abenbury WwTW | 1798 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335012 | 349326 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JY | LL130JY | ll13 0jy | ll130jy | Wrexham | Wrecsam | Abenbury WwTW | 1912 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 334869 | 349306 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0JZ | LL130JZ | ll13 0jz | ll130jz | Wrexham | Wrecsam | Abenbury WwTW | 1724 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335027 | 349201 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LA | LL130LA | ll13 0la | ll130la | Wrexham | Wrecsam | Abenbury WwTW | 1742 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 334951 | 349083 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LB | LL130LB | ll13 0lb | ll130lb | Wrexham | Wrecsam | Overton WwTW | 1475 | 694 | 600to700 | 1.39 | 1.01 | 0.74 | 12.92 | 6.89 | 7.61 | 337820 | 340741 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LD | LL130LD | ll13 0ld | ll130ld | Wrexham | Wrecsam | Overton WwTW | 830 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 337438 | 341733 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LE | LL130LE | ll13 0le | ll130le | Wrexham | Wrecsam | Overton WwTW | 2090 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 337414 | 339665 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LF | LL130LF | ll13 0lf | ll130lf | Wrexham | Wrecsam | Overton WwTW | 1886 | 709 | 700to900 | 1.42 | 1.04 | 0.76 | 13.2 | 7.04 | 7.78 | 336908 | 339734 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LG | LL130LG | ll13 0lg | ll130lg | Wrexham | Wrecsam | Overton WwTW | 1251 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 335886 | 340585 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LH | LL130LH | ll13 0lh | ll130lh | Wrexham | Wrecsam | Penley STW | 500 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341640 | 339987 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LJ | LL130LJ | ll13 0lj | ll130lj | Wrexham | Wrecsam | Overton WwTW | 1205 | 694 | 600to700 | 1.39 | 1.01 | 0.74 | 12.92 | 6.89 | 7.61 | 337814 | 341440 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LL | LL130LL | ll13 0ll | ll130ll | Wrexham | Wrecsam | Penley STW | 732 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341862 | 339836 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LN | LL130LN | ll13 0ln | ll130ln | Wrexham | Wrecsam | Penley STW | 754 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341790 | 339773 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LP | LL130LP | ll13 0lp | ll130lp | Wrexham | Wrecsam | Penley STW | 967 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341686 | 339516 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LQ | LL130LQ | ll13 0lq | ll130lq | Wrexham | Wrecsam | Penley STW | 446 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341513 | 340015 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LR | LL130LR | ll13 0lr | ll130lr | Wrexham | Wrecsam | Penley STW | 1211 | 682 | 600to700 | 1.36 | 1 | 0.73 | 12.68 | 6.76 | 7.48 | 341129 | 339301 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LS | LL130LS | ll13 0ls | ll130ls | Wrexham | Wrecsam | Penley STW | 886 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341976 | 339726 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LT | LL130LT | ll13 0lt | ll130lt | Wrexham | Wrecsam | Penley STW | 1484 | 692 | 600to700 | 1.38 | 1.01 | 0.74 | 12.88 | 6.87 | 7.59 | 342580 | 339465 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LU | LL130LU | ll13 0lu | ll130lu | Wrexham | Wrecsam | Penley STW | 606 | 674 | 600to700 | 1.34 | 0.98 | 0.72 | 12.53 | 6.68 | 7.39 | 340975 | 340125 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LW | LL130LW | ll13 0lw | ll130lw | Wrexham | Wrecsam | Penley STW | 775 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341841 | 339775 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LX | LL130LX | ll13 0lx | ll130lx | Wrexham | Wrecsam | Abenbury WwTW | 1774 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 334950 | 349159 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LY | LL130LY | ll13 0ly | ll130ly | Wrexham | Wrecsam | Penley STW | 1222 | 682 | 600to700 | 1.36 | 1 | 0.73 | 12.68 | 6.76 | 7.48 | 340338 | 340026 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0LZ | LL130LZ | ll13 0lz | ll130lz | Wrexham | Wrecsam | Abenbury WwTW | 1666 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335031 | 349077 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NA | LL130NA | ll13 0na | ll130na | Wrexham | Wrecsam | Penley STW | 2473 | 690 | 600to700 | 1.38 | 1.01 | 0.74 | 12.84 | 6.85 | 7.57 | 339196 | 339515 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NB | LL130NB | ll13 0nb | ll130nb | Wrexham | Wrecsam | Penley STW | 1954 | 682 | 600to700 | 1.36 | 1 | 0.73 | 12.68 | 6.76 | 7.48 | 339531 | 340336 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0ND | LL130ND | ll13 0nd | ll130nd | Wrexham | Wrecsam | Penley STW | 1255 | 676 | 600to700 | 1.35 | 0.99 | 0.72 | 12.57 | 6.7 | 7.41 | 340410 | 341115 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NE | LL130NE | ll13 0ne | ll130ne | Wrexham | Wrecsam | Penley STW | 551 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341817 | 340024 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NF | LL130NF | ll13 0nf | ll130nf | Wrexham | Wrecsam | Penley STW | 2010 | 668 | 600to700 | 1.33 | 0.97 | 0.71 | 12.41 | 6.62 | 7.32 | 340787 | 342346 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NG | LL130NG | ll13 0ng | ll130ng | Wrexham | Wrecsam | Penley STW | 292 | 673 | 600to700 | 1.34 | 0.98 | 0.72 | 12.51 | 6.67 | 7.37 | 341240 | 340627 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NH | LL130NH | ll13 0nh | ll130nh | Wrexham | Wrecsam | Penley STW | 322 | 674 | 600to700 | 1.34 | 0.98 | 0.72 | 12.53 | 6.68 | 7.39 | 341245 | 340240 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NJ | LL130NJ | ll13 0nj | ll130nj | Wrexham | Wrecsam | Abenbury WwTW | 2338 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334408 | 349329 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NL | LL130NL | ll13 0nl | ll130nl | Wrexham | Wrecsam | Penley STW | 1244 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 341508 | 339217 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NN | LL130NN | ll13 0nn | ll130nn | Wrexham | Wrecsam | Penley STW | 665 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341854 | 339911 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NP | LL130NP | ll13 0np | ll130np | Wrexham | Wrecsam | Abenbury WwTW | 2196 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 334550 | 349299 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NQ | LL130NQ | ll13 0nq | ll130nq | Wrexham | Wrecsam | Abenbury WwTW | 2136 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 334631 | 349330 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NR | LL130NR | ll13 0nr | ll130nr | Wrexham | Wrecsam | Abenbury WwTW | 2118 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 334613 | 349249 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NS | LL130NS | ll13 0ns | ll130ns | Wrexham | Wrecsam | Abenbury WwTW | 2188 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 334535 | 349243 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NT | LL130NT | ll13 0nt | ll130nt | Wrexham | Wrecsam | Abenbury WwTW | 1664 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335060 | 349135 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NU | LL130NU | ll13 0nu | ll130nu | Wrexham | Wrecsam | Abenbury WwTW | 1284 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 335538 | 349188 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NW | LL130NW | ll13 0nw | ll130nw | Wrexham | Wrecsam | Penley STW | 1161 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 341565 | 339303 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NX | LL130NX | ll13 0nx | ll130nx | Wrexham | Wrecsam | Abenbury WwTW | 2273 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334468 | 349304 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NY | LL130NY | ll13 0ny | ll130ny | Wrexham | Wrecsam | Abenbury WwTW | 1182 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 335877 | 349371 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0NZ | LL130NZ | ll13 0nz | ll130nz | Wrexham | Wrecsam | Abenbury WwTW | 2289 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334485 | 349381 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PA | LL130PA | ll13 0pa | ll130pa | Wrexham | Wrecsam | Abenbury WwTW | 96 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 336598 | 348488 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PB | LL130PB | ll13 0pb | ll130pb | Wrexham | Wrecsam | Abenbury WwTW | 1198 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 336061 | 349494 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PD | LL130PD | ll13 0pd | ll130pd | Wrexham | Wrecsam | Abenbury WwTW | 1141 | 707 | 700to900 | 1.41 | 1.03 | 0.76 | 13.16 | 7.02 | 7.76 | 336576 | 349543 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PE | LL130PE | ll13 0pe | ll130pe | Wrexham | Wrecsam | Abenbury WwTW | 1649 | 707 | 700to900 | 1.41 | 1.03 | 0.76 | 13.16 | 7.02 | 7.76 | 337262 | 349892 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PF | LL130PF | ll13 0pf | ll130pf | Wrexham | Wrecsam | Abenbury WwTW | 1317 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 335256 | 348181 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PG | LL130PG | ll13 0pg | ll130pg | Wrexham | Wrecsam | Abenbury WwTW | 1291 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 335303 | 348087 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PH | LL130PH | ll13 0ph | ll130ph | Wrexham | Wrecsam | Abenbury WwTW | 1217 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335516 | 347769 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PJ | LL130PJ | ll13 0pj | ll130pj | Wrexham | Wrecsam | Abenbury WwTW | 1163 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 335641 | 349123 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PL | LL130PL | ll13 0pl | ll130pl | Wrexham | Wrecsam | Abenbury WwTW | 1203 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335515 | 347798 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PN | LL130PN | ll13 0pn | ll130pn | Wrexham | Wrecsam | Abenbury WwTW | 1164 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335569 | 347783 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PP | LL130PP | ll13 0pp | ll130pp | Wrexham | Wrecsam | Abenbury WwTW | 1120 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335642 | 347754 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PQ | LL130PQ | ll13 0pq | ll130pq | Wrexham | Wrecsam | Abenbury WwTW | 2276 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335242 | 350262 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PR | LL130PR | ll13 0pr | ll130pr | Wrexham | Wrecsam | Abenbury WwTW | 1108 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335674 | 347731 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PS | LL130PS | ll13 0ps | ll130ps | Wrexham | Wrecsam | Abenbury WwTW | 1251 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 335385 | 347960 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PT | LL130PT | ll13 0pt | ll130pt | Wrexham | Wrecsam | Abenbury WwTW | 1214 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 335463 | 347872 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PU | LL130PU | ll13 0pu | ll130pu | Wrexham | Wrecsam | Abenbury WwTW | 1186 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 335464 | 347936 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PW | LL130PW | ll13 0pw | ll130pw | Wrexham | Wrecsam | Abenbury WwTW | 1141 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335603 | 347774 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PX | LL130PX | ll13 0px | ll130px | Wrexham | Wrecsam | Abenbury WwTW | 1164 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 335665 | 349153 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PY | LL130PY | ll13 0py | ll130py | Wrexham | Wrecsam | Abenbury WwTW | 1078 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335569 | 347967 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0PZ | LL130PZ | ll13 0pz | ll130pz | Wrexham | Wrecsam | Abenbury WwTW | 1179 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 335564 | 349042 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QA | LL130QA | ll13 0qa | ll130qa | Wrexham | Wrecsam | Abenbury WwTW | 1580 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337628 | 347245 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QB | LL130QB | ll13 0qb | ll130qb | Wrexham | Wrecsam | Abenbury WwTW | 1552 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337691 | 347348 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QD | LL130QD | ll13 0qd | ll130qd | Wrexham | Wrecsam | Abenbury WwTW | 1286 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335458 | 349075 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QE | LL130QE | ll13 0qe | ll130qe | Wrexham | Wrecsam | Penley STW | 333 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341631 | 340163 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QF | LL130QF | ll13 0qf | ll130qf | Wrexham | Wrecsam | Abenbury WwTW | 1282 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 335514 | 349151 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QG | LL130QG | ll13 0qg | ll130qg | Wrexham | Wrecsam | Abenbury WwTW | 1310 | 722 | 700to900 | 1.44 | 1.06 | 0.77 | 13.45 | 7.17 | 7.93 | 335546 | 349239 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QH | LL130QH | ll13 0qh | ll130qh | Wrexham | Wrecsam | Abenbury WwTW | 1417 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335372 | 349183 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QJ | LL130QJ | ll13 0qj | ll130qj | Wrexham | Wrecsam | Penley STW | 931 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341665 | 339548 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QL | LL130QL | ll13 0ql | ll130ql | Wrexham | Wrecsam | Abenbury WwTW | 1320 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335431 | 349095 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QN | LL130QN | ll13 0qn | ll130qn | Wrexham | Wrecsam | Abenbury WwTW | 1385 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335366 | 349114 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QP | LL130QP | ll13 0qp | ll130qp | Wrexham | Wrecsam | Abenbury WwTW | 1844 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 334864 | 349139 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QQ | LL130QQ | ll13 0qq | ll130qq | Wrexham | Wrecsam | Penley STW | 447 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341690 | 340066 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0QR | LL130QR | ll13 0qr | ll130qr | Wrexham | Wrecsam | Abenbury WwTW | 1487 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335328 | 349243 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RA | LL130RA | ll13 0ra | ll130ra | Wrexham | Wrecsam | Abenbury WwTW | 976 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335688 | 347954 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RB | LL130RB | ll13 0rb | ll130rb | Wrexham | Wrecsam | Abenbury WwTW | 1146 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 335489 | 347982 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RD | LL130RD | ll13 0rd | ll130rd | Wrexham | Wrecsam | Abenbury WwTW | 1008 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335635 | 347990 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RE | LL130RE | ll13 0re | ll130re | Wrexham | Wrecsam | Abenbury WwTW | 1205 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 335433 | 347963 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RF | LL130RF | ll13 0rf | ll130rf | Wrexham | Wrecsam | Abenbury WwTW | 1092 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335523 | 348044 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RG | LL130RG | ll13 0rg | ll130rg | Wrexham | Wrecsam | Abenbury WwTW | 948 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335732 | 347931 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RH | LL130RH | ll13 0rh | ll130rh | Wrexham | Wrecsam | Abenbury WwTW | 1036 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335701 | 347816 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RJ | LL130RJ | ll13 0rj | ll130rj | Wrexham | Wrecsam | Abenbury WwTW | 931 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335768 | 347905 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RL | LL130RL | ll13 0rl | ll130rl | Wrexham | Wrecsam | Abenbury WwTW | 1157 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335536 | 347854 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RN | LL130RN | ll13 0rn | ll130rn | Wrexham | Wrecsam | Abenbury WwTW | 993 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335728 | 347853 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RP | LL130RP | ll13 0rp | ll130rp | Wrexham | Wrecsam | Abenbury WwTW | 1145 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335519 | 347915 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RQ | LL130RQ | ll13 0rq | ll130rq | Wrexham | Wrecsam | Abenbury WwTW | 868 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335808 | 347960 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RR | LL130RR | ll13 0rr | ll130rr | Wrexham | Wrecsam | Abenbury WwTW | 1089 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335587 | 347904 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RS | LL130RS | ll13 0rs | ll130rs | Wrexham | Wrecsam | Abenbury WwTW | 1023 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335660 | 347907 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RT | LL130RT | ll13 0rt | ll130rt | Wrexham | Wrecsam | Abenbury WwTW | 948 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335830 | 347792 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RU | LL130RU | ll13 0ru | ll130ru | Wrexham | Wrecsam | Abenbury WwTW | 934 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335946 | 347695 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RW | LL130RW | ll13 0rw | ll130rw | Wrexham | Wrecsam | Abenbury WwTW | 1085 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335604 | 347880 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RX | LL130RX | ll13 0rx | ll130rx | Wrexham | Wrecsam | Abenbury WwTW | 865 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 336091 | 347673 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RY | LL130RY | ll13 0ry | ll130ry | Wrexham | Wrecsam | Abenbury WwTW | 961 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 336051 | 347584 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0RZ | LL130RZ | ll13 0rz | ll130rz | Wrexham | Wrecsam | Abenbury WwTW | 1501 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337599 | 347326 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SA | LL130SA | ll13 0sa | ll130sa | Wrexham | Wrecsam | Abenbury WwTW | 974 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335901 | 347681 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SB | LL130SB | ll13 0sb | ll130sb | Wrexham | Wrecsam | Abenbury WwTW | 914 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 336146 | 347586 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SD | LL130SD | ll13 0sd | ll130sd | Wrexham | Wrecsam | Abenbury WwTW | 1049 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335795 | 347679 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SE | LL130SE | ll13 0se | ll130se | Wrexham | Wrecsam | Abenbury WwTW | 1012 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335971 | 347576 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SF | LL130SF | ll13 0sf | ll130sf | Wrexham | Wrecsam | Abenbury WwTW | 1013 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335985 | 347565 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SG | LL130SG | ll13 0sg | ll130sg | Wrexham | Wrecsam | Abenbury WwTW | 1222 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 335383 | 348056 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SH | LL130SH | ll13 0sh | ll130sh | Wrexham | Wrecsam | Abenbury WwTW | 1244 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 335346 | 348107 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SJ | LL130SJ | ll13 0sj | ll130sj | Wrexham | Wrecsam | Penley STW | 880 | 677 | 600to700 | 1.35 | 0.99 | 0.72 | 12.59 | 6.71 | 7.42 | 341848 | 339661 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SL | LL130SL | ll13 0sl | ll130sl | Wrexham | Wrecsam | Bangor On Dee STW | 2785 | 697 | 600to700 | 1.39 | 1.02 | 0.75 | 12.97 | 6.92 | 7.65 | 336828 | 345258 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SN | LL130SN | ll13 0sn | ll130sn | Wrexham | Wrecsam | Erbistock STW | 2126 | 702 | 700to900 | 1.4 | 1.03 | 0.75 | 13.07 | 6.97 | 7.7 | 335695 | 344143 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SP | LL130SP | ll13 0sp | ll130sp | Wrexham | Wrecsam | Abenbury WwTW | 3114 | 711 | 700to900 | 1.42 | 1.04 | 0.76 | 13.24 | 7.06 | 7.81 | 335535 | 345462 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SQ | LL130SQ | ll13 0sq | ll130sq | Wrexham | Wrecsam | Abenbury WwTW | 1138 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 337310 | 347553 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SR | LL130SR | ll13 0sr | ll130sr | Wrexham | Wrecsam | Abenbury WwTW | 1716 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 334839 | 348396 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SS | LL130SS | ll13 0ss | ll130ss | Wrexham | Wrecsam | Abenbury WwTW | 2077 | 736 | 700to900 | 1.47 | 1.08 | 0.79 | 13.72 | 7.32 | 8.09 | 334505 | 348070 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0ST | LL130ST | ll13 0st | ll130st | Wrexham | Wrecsam | Abenbury WwTW | 2229 | 732 | 700to900 | 1.46 | 1.07 | 0.79 | 13.64 | 7.27 | 8.04 | 334631 | 347278 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SU | LL130SU | ll13 0su | ll130su | Wrexham | Wrecsam | Abenbury WwTW | 2756 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335452 | 345878 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SW | LL130SW | ll13 0sw | ll130sw | Wrexham | Wrecsam | Erbistock STW | 2972 | 720 | 700to900 | 1.44 | 1.05 | 0.77 | 13.41 | 7.15 | 7.91 | 334842 | 344934 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SX | LL130SX | ll13 0sx | ll130sx | Wrexham | Wrecsam | Abenbury WwTW | 1718 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337694 | 347119 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SY | LL130SY | ll13 0sy | ll130sy | Wrexham | Wrecsam | Abenbury WwTW | 2357 | 713 | 700to900 | 1.43 | 1.04 | 0.76 | 13.28 | 7.08 | 7.83 | 335997 | 346114 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0SZ | LL130SZ | ll13 0sz | ll130sz | Wrexham | Wrecsam | Abenbury WwTW | 1121 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 335708 | 347668 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TA | LL130TA | ll13 0ta | ll130ta | Wrexham | Wrecsam | Abenbury WwTW | 1941 | 713 | 700to900 | 1.43 | 1.04 | 0.76 | 13.28 | 7.08 | 7.83 | 336250 | 346487 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TB | LL130TB | ll13 0tb | ll130tb | Wrexham | Wrecsam | Abenbury WwTW | 1819 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 336839 | 346607 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TD | LL130TD | ll13 0td | ll130td | Wrexham | Wrecsam | Abenbury WwTW | 2173 | 696 | 600to700 | 1.39 | 1.02 | 0.75 | 12.95 | 6.91 | 7.64 | 336903 | 346259 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TE | LL130TE | ll13 0te | ll130te | Wrexham | Wrecsam | Abenbury WwTW | 1738 | 715 | 700to900 | 1.43 | 1.05 | 0.77 | 13.32 | 7.1 | 7.85 | 335809 | 346833 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TF | LL130TF | ll13 0tf | ll130tf | Wrexham | Wrecsam | Abenbury WwTW | 1084 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 337057 | 347443 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TG | LL130TG | ll13 0tg | ll130tg | Wrexham | Wrecsam | Abenbury WwTW | 1819 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 337421 | 346805 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TH | LL130TH | ll13 0th | ll130th | Wrexham | Wrecsam | Abenbury WwTW | 1764 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337531 | 346935 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TJ | LL130TJ | ll13 0tj | ll130tj | Wrexham | Wrecsam | Abenbury WwTW | 1692 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337714 | 347172 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TL | LL130TL | ll13 0tl | ll130tl | Wrexham | Wrecsam | Abenbury WwTW | 1757 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337618 | 347006 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TN | LL130TN | ll13 0tn | ll130tn | Wrexham | Wrecsam | Abenbury WwTW | 1884 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337646 | 346868 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TP | LL130TP | ll13 0tp | ll130tp | Wrexham | Wrecsam | Bangor On Dee STW | 1646 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337869 | 346258 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TQ | LL130TQ | ll13 0tq | ll130tq | Wrexham | Wrecsam | Abenbury WwTW | 1749 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337744 | 347122 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TR | LL130TR | ll13 0tr | ll130tr | Wrexham | Wrecsam | Abenbury WwTW | 1617 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337604 | 347174 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TS | LL130TS | ll13 0ts | ll130ts | Wrexham | Wrecsam | Abenbury WwTW | 951 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 337453 | 348095 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TT | LL130TT | ll13 0tt | ll130tt | Wrexham | Wrecsam | Abenbury WwTW | 1688 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337578 | 347062 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TU | LL130TU | ll13 0tu | ll130tu | Wrexham | Wrecsam | Abenbury WwTW | 1819 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337775 | 347055 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TW | LL130TW | ll13 0tw | ll130tw | Wrexham | Wrecsam | Bangor On Dee STW | 1655 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337935 | 346577 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TX | LL130TX | ll13 0tx | ll130tx | Wrexham | Wrecsam | Abenbury WwTW | 1743 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337690 | 347082 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0TY | LL130TY | ll13 0ty | ll130ty | Wrexham | Wrecsam | Abenbury WwTW | 1803 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337943 | 347255 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UA | LL130UA | ll13 0ua | ll130ua | Wrexham | Wrecsam | Abenbury WwTW | 1683 | 691 | 600to700 | 1.38 | 1.01 | 0.74 | 12.86 | 6.86 | 7.58 | 338013 | 347565 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UB | LL130UB | ll13 0ub | ll130ub | Wrexham | Wrecsam | Abenbury WwTW | 1777 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337742 | 347083 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UD | LL130UD | ll13 0ud | ll130ud | Wrexham | Wrecsam | Abenbury WwTW | 1785 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337837 | 347163 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UE | LL130UE | ll13 0ue | ll130ue | Wrexham | Wrecsam | Bangor On Dee STW | 1306 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 338390 | 346728 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UF | LL130UF | ll13 0uf | ll130uf | Wrexham | Wrecsam | Bowling Bank STW | 865 | 671 | 600to700 | 1.34 | 0.98 | 0.72 | 12.47 | 6.65 | 7.35 | 339488 | 347380 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UG | LL130UG | ll13 0ug | ll130ug | Wrexham | Wrecsam | Five Fords STW | 711 | 664 | 600to700 | 1.32 | 0.97 | 0.71 | 12.33 | 6.58 | 7.27 | 340198 | 347209 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UH | LL130UH | ll13 0uh | ll130uh | Wrexham | Wrecsam | Bowling Bank STW | 383 | 671 | 600to700 | 1.34 | 0.98 | 0.72 | 12.47 | 6.65 | 7.35 | 339531 | 348039 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UJ | LL130UJ | ll13 0uj | ll130uj | Wrexham | Wrecsam | Abenbury WwTW | 1760 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337826 | 347187 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UL | LL130UL | ll13 0ul | ll130ul | Wrexham | Wrecsam | Bowling Bank STW | 1114 | 676 | 600to700 | 1.35 | 0.99 | 0.72 | 12.57 | 6.7 | 7.41 | 338829 | 347835 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UN | LL130UN | ll13 0un | ll130un | Wrexham | Wrecsam | Bowling Bank STW | 1350 | 676 | 600to700 | 1.35 | 0.99 | 0.72 | 12.57 | 6.7 | 7.41 | 338551 | 348160 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UP | LL130UP | ll13 0up | ll130up | Wrexham | Wrecsam | Bowling Bank STW | 1277 | 676 | 600to700 | 1.35 | 0.99 | 0.72 | 12.57 | 6.7 | 7.41 | 338671 | 347796 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UQ | LL130UQ | ll13 0uq | ll130uq | Wrexham | Wrecsam | Abenbury WwTW | 1692 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337776 | 347234 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UR | LL130UR | ll13 0ur | ll130ur | Wrexham | Wrecsam | Bangor On Dee STW | 1877 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 338149 | 347342 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0US | LL130US | ll13 0us | ll130us | Wrexham | Wrecsam | Abenbury WwTW | 1515 | 691 | 600to700 | 1.38 | 1.01 | 0.74 | 12.86 | 6.86 | 7.58 | 338030 | 348066 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UU | LL130UU | ll13 0uu | ll130uu | Wrexham | Wrecsam | Abenbury WwTW | 3307 | 778 | 700to900 | 1.56 | 1.14 | 0.84 | 14.5 | 7.73 | 8.55 | 333304 | 347798 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UX | LL130UX | ll13 0ux | ll130ux | Wrexham | Wrecsam | Abenbury WwTW | 1634 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337651 | 347193 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UY | LL130UY | ll13 0uy | ll130uy | Wrexham | Wrecsam | Abenbury WwTW | 3175 | 754 | 700to900 | 1.51 | 1.1 | 0.81 | 14.05 | 7.5 | 8.28 | 333536 | 347421 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0UZ | LL130UZ | ll13 0uz | ll130uz | Wrexham | Wrecsam | Abenbury WwTW | 1618 | 685 | 600to700 | 1.37 | 1 | 0.73 | 12.74 | 6.8 | 7.51 | 337744 | 347308 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YA | LL130YA | ll13 0ya | ll130ya | Wrexham | Wrecsam | Abenbury WwTW | 3231 | 754 | 700to900 | 1.51 | 1.1 | 0.81 | 14.05 | 7.5 | 8.28 | 333843 | 346647 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YB | LL130YB | ll13 0yb | ll130yb | Wrexham | Wrecsam | Abenbury WwTW | 3887 | 762 | 700to900 | 1.53 | 1.12 | 0.82 | 14.2 | 7.57 | 8.37 | 333704 | 345762 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YD | LL130YD | ll13 0yd | ll130yd | Wrexham | Wrecsam | Erbistock STW | 3463 | 754 | 700to900 | 1.51 | 1.1 | 0.81 | 14.05 | 7.5 | 8.28 | 333799 | 345062 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YE | LL130YE | ll13 0ye | ll130ye | Wrexham | Wrecsam | Erbistock STW | 2999 | 784 | 700to900 | 1.57 | 1.15 | 0.84 | 14.61 | 7.79 | 8.61 | 332779 | 343351 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YF | LL130YF | ll13 0yf | ll130yf | Wrexham | Wrecsam | Erbistock STW | 3341 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333278 | 344550 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YG | LL130YG | ll13 0yg | ll130yg | Wrexham | Wrecsam | Erbistock STW | 3397 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333477 | 344780 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YH | LL130YH | ll13 0yh | ll130yh | Wrexham | Wrecsam | Erbistock STW | 3977 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 332887 | 345052 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YJ | LL130YJ | ll13 0yj | ll130yj | Wrexham | Wrecsam | Abenbury WwTW | 2306 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334531 | 349509 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YL | LL130YL | ll13 0yl | ll130yl | Wrexham | Wrecsam | Erbistock STW | 4941 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332134 | 345673 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YN | LL130YN | ll13 0yn | ll130yn | Wrexham | Wrecsam | Erbistock STW | 4727 | 802 | 700to900 | 1.61 | 1.17 | 0.86 | 14.95 | 7.97 | 8.81 | 332368 | 345594 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YP | LL130YP | ll13 0yp | ll130yp | Wrexham | Wrecsam | Abenbury WwTW | 4539 | 807 | 700to900 | 1.62 | 1.18 | 0.87 | 15.04 | 8.02 | 8.87 | 332302 | 346818 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YR | LL130YR | ll13 0yr | ll130yr | Wrexham | Wrecsam | Abenbury WwTW | 4693 | 809 | 700to900 | 1.62 | 1.18 | 0.87 | 15.08 | 8.04 | 8.89 | 331922 | 347660 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YS | LL130YS | ll13 0ys | ll130ys | Wrexham | Wrecsam | Abenbury WwTW | 3991 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 332589 | 348843 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YT | LL130YT | ll13 0yt | ll130yt | Wrexham | Wrecsam | Abenbury WwTW | 3950 | 778 | 700to900 | 1.56 | 1.14 | 0.84 | 14.5 | 7.73 | 8.55 | 332618 | 348093 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YU | LL130YU | ll13 0yu | ll130yu | Wrexham | Wrecsam | Abenbury WwTW | 2328 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334463 | 349424 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YW | LL130YW | ll13 0yw | ll130yw | Wrexham | Wrecsam | Abenbury WwTW | 3850 | 784 | 700to900 | 1.57 | 1.15 | 0.84 | 14.61 | 7.79 | 8.61 | 333057 | 346796 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 0YY | LL130YY | ll13 0yy | ll130yy | Wrexham | Wrecsam | Abenbury WwTW | 2204 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 334593 | 349407 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AA | LL137AA | ll13 7aa | ll137aa | Wrexham | Wrecsam | Abenbury WwTW | 3409 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333602 | 350106 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AB | LL137AB | ll13 7ab | ll137ab | Wrexham | Wrecsam | Abenbury WwTW | 3432 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333550 | 350061 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AD | LL137AD | ll13 7ad | ll137ad | Wrexham | Wrecsam | Abenbury WwTW | 3286 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333626 | 349891 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AE | LL137AE | ll13 7ae | ll137ae | Wrexham | Wrecsam | Abenbury WwTW | 3573 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333325 | 349930 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AF | LL137AF | ll13 7af | ll137af | Wrexham | Wrecsam | Abenbury WwTW | 3183 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333712 | 349834 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AG | LL137AG | ll13 7ag | ll137ag | Wrexham | Wrecsam | Abenbury WwTW | 5137 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 331908 | 350590 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AH | LL137AH | ll13 7ah | ll137ah | Wrexham | Wrecsam | Abenbury WwTW | 3668 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333118 | 349683 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AN | LL137AN | ll13 7an | ll137an | Wrexham | Wrecsam | Abenbury WwTW | 3120 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333765 | 349799 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AP | LL137AP | ll13 7ap | ll137ap | Wrexham | Wrecsam | Abenbury WwTW | 3195 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333552 | 349493 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AR | LL137AR | ll13 7ar | ll137ar | Wrexham | Wrecsam | Abenbury WwTW | 3091 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333743 | 349686 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AS | LL137AS | ll13 7as | ll137as | Wrexham | Wrecsam | Abenbury WwTW | 3301 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333539 | 349744 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AT | LL137AT | ll13 7at | ll137at | Wrexham | Wrecsam | Abenbury WwTW | 3225 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333589 | 349668 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AU | LL137AU | ll13 7au | ll137au | Wrexham | Wrecsam | Abenbury WwTW | 3004 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333796 | 349592 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7AW | LL137AW | ll13 7aw | ll137aw | Wrexham | Wrecsam | Abenbury WwTW | 3149 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333658 | 349638 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BA | LL137BA | ll13 7ba | ll137ba | Wrexham | Wrecsam | Abenbury WwTW | 3009 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333779 | 349563 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BB | LL137BB | ll13 7bb | ll137bb | Wrexham | Wrecsam | Abenbury WwTW | 2971 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333807 | 349531 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BD | LL137BD | ll13 7bd | ll137bd | Wrexham | Wrecsam | Abenbury WwTW | 2954 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333812 | 349500 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BE | LL137BE | ll13 7be | ll137be | Wrexham | Wrecsam | Abenbury WwTW | 2925 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333833 | 349473 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BG | LL137BG | ll13 7bg | ll137bg | Wrexham | Wrecsam | Abenbury WwTW | 2938 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333805 | 349436 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BH | LL137BH | ll13 7bh | ll137bh | Wrexham | Wrecsam | Abenbury WwTW | 2910 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333819 | 349394 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BL | LL137BL | ll13 7bl | ll137bl | Wrexham | Wrecsam | Abenbury WwTW | 2973 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333743 | 349368 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BN | LL137BN | ll13 7bn | ll137bn | Wrexham | Wrecsam | Abenbury WwTW | 2597 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334028 | 349002 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BS | LL137BS | ll13 7bs | ll137bs | Wrexham | Wrecsam | Abenbury WwTW | 2775 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334004 | 349496 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BT | LL137BT | ll13 7bt | ll137bt | Wrexham | Wrecsam | Abenbury WwTW | 2946 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333886 | 349649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BU | LL137BU | ll13 7bu | ll137bu | Wrexham | Wrecsam | Abenbury WwTW | 3028 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333799 | 349658 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BW | LL137BW | ll13 7bw | ll137bw | Wrexham | Wrecsam | Abenbury WwTW | 2927 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333760 | 349273 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7BY | LL137BY | ll13 7by | ll137by | Wrexham | Wrecsam | Abenbury WwTW | 3279 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333586 | 349793 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DA | LL137DA | ll13 7da | ll137da | Wrexham | Wrecsam | Abenbury WwTW | 2643 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334009 | 349112 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DD | LL137DD | ll13 7dd | ll137dd | Wrexham | Wrecsam | Abenbury WwTW | 3547 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333383 | 349990 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DE | LL137DE | ll13 7de | ll137de | Wrexham | Wrecsam | Abenbury WwTW | 3567 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333353 | 349975 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DF | LL137DF | ll13 7df | ll137df | Wrexham | Wrecsam | Abenbury WwTW | 3563 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333384 | 350028 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DG | LL137DG | ll13 7dg | ll137dg | Wrexham | Wrecsam | Abenbury WwTW | 3484 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333400 | 349881 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DH | LL137DH | ll13 7dh | ll137dh | Wrexham | Wrecsam | Abenbury WwTW | 3491 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333383 | 349860 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DJ | LL137DJ | ll13 7dj | ll137dj | Wrexham | Wrecsam | Abenbury WwTW | 3497 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333345 | 349789 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DL | LL137DL | ll13 7dl | ll137dl | Wrexham | Wrecsam | Abenbury WwTW | 3468 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333411 | 349866 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DN | LL137DN | ll13 7dn | ll137dn | Wrexham | Wrecsam | Abenbury WwTW | 3545 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333330 | 349875 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DP | LL137DP | ll13 7dp | ll137dp | Wrexham | Wrecsam | Abenbury WwTW | 3498 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333312 | 349714 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DQ | LL137DQ | ll13 7dq | ll137dq | Wrexham | Wrecsam | Abenbury WwTW | 3414 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333362 | 349610 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DR | LL137DR | ll13 7dr | ll137dr | Wrexham | Wrecsam | Abenbury WwTW | 3540 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333250 | 349671 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DS | LL137DS | ll13 7ds | ll137ds | Wrexham | Wrecsam | Abenbury WwTW | 3571 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333165 | 349524 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DT | LL137DT | ll13 7dt | ll137dt | Wrexham | Wrecsam | Abenbury WwTW | 3612 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333068 | 349345 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DU | LL137DU | ll13 7du | ll137du | Wrexham | Wrecsam | Abenbury WwTW | 3478 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333375 | 349812 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DW | LL137DW | ll13 7dw | ll137dw | Wrexham | Wrecsam | Abenbury WwTW | 3541 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333305 | 349808 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DX | LL137DX | ll13 7dx | ll137dx | Wrexham | Wrecsam | Abenbury WwTW | 2871 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333702 | 348724 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DY | LL137DY | ll13 7dy | ll137dy | Wrexham | Wrecsam | Abenbury WwTW | 3432 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333390 | 349729 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7DZ | LL137DZ | ll13 7dz | ll137dz | Wrexham | Wrecsam | Abenbury WwTW | 2808 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333765 | 348724 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EA | LL137EA | ll13 7ea | ll137ea | Wrexham | Wrecsam | Abenbury WwTW | 3322 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333480 | 349660 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EB | LL137EB | ll13 7eb | ll137eb | Wrexham | Wrecsam | Abenbury WwTW | 3252 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333491 | 349492 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7ED | LL137ED | ll13 7ed | ll137ed | Wrexham | Wrecsam | Abenbury WwTW | 3201 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333489 | 349323 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EE | LL137EE | ll13 7ee | ll137ee | Wrexham | Wrecsam | Abenbury WwTW | 3364 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333445 | 349685 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EF | LL137EF | ll13 7ef | ll137ef | Wrexham | Wrecsam | Abenbury WwTW | 3297 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333450 | 349510 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EG | LL137EG | ll13 7eg | ll137eg | Wrexham | Wrecsam | Abenbury WwTW | 3386 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333405 | 349645 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EH | LL137EH | ll13 7eh | ll137eh | Wrexham | Wrecsam | Abenbury WwTW | 3473 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333315 | 349653 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EJ | LL137EJ | ll13 7ej | ll137ej | Wrexham | Wrecsam | Abenbury WwTW | 2937 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333636 | 348728 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EL | LL137EL | ll13 7el | ll137el | Wrexham | Wrecsam | Abenbury WwTW | 3513 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333273 | 349654 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EN | LL137EN | ll13 7en | ll137en | Wrexham | Wrecsam | Abenbury WwTW | 3225 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333411 | 349121 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EP | LL137EP | ll13 7ep | ll137ep | Wrexham | Wrecsam | Abenbury WwTW | 2719 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333868 | 348818 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EQ | LL137EQ | ll13 7eq | ll137eq | Wrexham | Wrecsam | Abenbury WwTW | 2903 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333675 | 348769 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7ER | LL137ER | ll13 7er | ll137er | Wrexham | Wrecsam | Abenbury WwTW | 3209 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333451 | 349218 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7ES | LL137ES | ll13 7es | ll137es | Wrexham | Wrecsam | Abenbury WwTW | 3356 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333412 | 349579 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7ET | LL137ET | ll13 7et | ll137et | Wrexham | Wrecsam | Abenbury WwTW | 3243 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333456 | 349357 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EU | LL137EU | ll13 7eu | ll137eu | Wrexham | Wrecsam | Abenbury WwTW | 3523 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333336 | 349834 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EW | LL137EW | ll13 7ew | ll137ew | Wrexham | Wrecsam | Abenbury WwTW | 3392 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333340 | 349483 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EX | LL137EX | ll13 7ex | ll137ex | Wrexham | Wrecsam | Abenbury WwTW | 2916 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333664 | 348784 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EY | LL137EY | ll13 7ey | ll137ey | Wrexham | Wrecsam | Abenbury WwTW | 3067 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333609 | 349257 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7EZ | LL137EZ | ll13 7ez | ll137ez | Wrexham | Wrecsam | Abenbury WwTW | 3018 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333560 | 348771 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7GT | LL137GT | ll13 7gt | ll137gt | Wrexham | Wrecsam | Abenbury WwTW | 4226 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 332431 | 349323 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7GU | LL137GU | ll13 7gu | ll137gu | Wrexham | Wrecsam | Abenbury WwTW | 2798 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333850 | 349119 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7GW | LL137GW | ll13 7gw | ll137gw | Wrexham | Wrecsam | Abenbury WwTW | 2808 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333827 | 349070 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7GX | LL137GX | ll13 7gx | ll137gx | Wrexham | Wrecsam | Abenbury WwTW | 2875 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333761 | 349081 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7GY | LL137GY | ll13 7gy | ll137gy | Wrexham | Wrecsam | Abenbury WwTW | 2865 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333754 | 349003 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7GZ | LL137GZ | ll13 7gz | ll137gz | Wrexham | Wrecsam | Abenbury WwTW | 2694 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333943 | 349062 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HA | LL137HA | ll13 7ha | ll137ha | Wrexham | Wrecsam | Abenbury WwTW | 3224 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333540 | 349543 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HB | LL137HB | ll13 7hb | ll137hb | Wrexham | Wrecsam | Abenbury WwTW | 3258 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333526 | 349601 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HD | LL137HD | ll13 7hd | ll137hd | Wrexham | Wrecsam | Abenbury WwTW | 3354 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333535 | 349861 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HE | LL137HE | ll13 7he | ll137he | Wrexham | Wrecsam | Abenbury WwTW | 3315 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333572 | 349849 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HF | LL137HF | ll13 7hf | ll137hf | Wrexham | Wrecsam | Abenbury WwTW | 3125 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333578 | 349353 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HG | LL137HG | ll13 7hg | ll137hg | Wrexham | Wrecsam | Abenbury WwTW | 3036 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333612 | 349147 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HH | LL137HH | ll13 7hh | ll137hh | Wrexham | Wrecsam | Abenbury WwTW | 3057 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333635 | 349308 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HJ | LL137HJ | ll13 7hj | ll137hj | Wrexham | Wrecsam | Abenbury WwTW | 2998 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333636 | 349086 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HL | LL137HL | ll13 7hl | ll137hl | Wrexham | Wrecsam | Abenbury WwTW | 3025 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333666 | 349300 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HN | LL137HN | ll13 7hn | ll137hn | Wrexham | Wrecsam | Abenbury WwTW | 3645 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333390 | 350211 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HP | LL137HP | ll13 7hp | ll137hp | Wrexham | Wrecsam | Abenbury WwTW | 3581 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333378 | 350055 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HQ | LL137HQ | ll13 7hq | ll137hq | Wrexham | Wrecsam | Abenbury WwTW | 3107 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333546 | 349175 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HS | LL137HS | ll13 7hs | ll137hs | Wrexham | Wrecsam | Abenbury WwTW | 3592 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333272 | 349859 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HT | LL137HT | ll13 7ht | ll137ht | Wrexham | Wrecsam | Abenbury WwTW | 3634 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333327 | 350072 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HU | LL137HU | ll13 7hu | ll137hu | Wrexham | Wrecsam | Abenbury WwTW | 3598 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333309 | 349955 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HX | LL137HX | ll13 7hx | ll137hx | Wrexham | Wrecsam | Abenbury WwTW | 3138 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333509 | 349155 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7HY | LL137HY | ll13 7hy | ll137hy | Wrexham | Wrecsam | Abenbury WwTW | 3623 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333267 | 349923 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7JA | LL137JA | ll13 7ja | ll137ja | Wrexham | Wrecsam | Abenbury WwTW | 3299 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333338 | 349135 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7JB | LL137JB | ll13 7jb | ll137jb | Wrexham | Wrecsam | Abenbury WwTW | 2953 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333647 | 348917 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7JD | LL137JD | ll13 7jd | ll137jd | Wrexham | Wrecsam | Abenbury WwTW | 2864 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333720 | 348807 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7JE | LL137JE | ll13 7je | ll137je | Wrexham | Wrecsam | Abenbury WwTW | 2988 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333603 | 348862 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7JF | LL137JF | ll13 7jf | ll137jf | Wrexham | Wrecsam | Abenbury WwTW | 2965 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 333625 | 348856 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7JG | LL137JG | ll13 7jg | ll137jg | Wrexham | Wrecsam | Abenbury WwTW | 3634 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333286 | 349990 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7LD | LL137LD | ll13 7ld | ll137ld | Wrexham | Wrecsam | Abenbury WwTW | 3717 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333309 | 350214 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7LG | LL137LG | ll13 7lg | ll137lg | Wrexham | Wrecsam | Abenbury WwTW | 3687 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333245 | 350026 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7LH | LL137LH | ll13 7lh | ll137lh | Wrexham | Wrecsam | Abenbury WwTW | 3631 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333370 | 350145 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7LL | LL137LL | ll13 7ll | ll137ll | Wrexham | Wrecsam | Abenbury WwTW | 3652 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333368 | 350186 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7LT | LL137LT | ll13 7lt | ll137lt | Wrexham | Wrecsam | Abenbury WwTW | 3839 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333195 | 350260 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7LU | LL137LU | ll13 7lu | ll137lu | Wrexham | Wrecsam | Abenbury WwTW | 3739 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333289 | 350222 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7LW | LL137LW | ll13 7lw | ll137lw | Wrexham | Wrecsam | Abenbury WwTW | 3868 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333208 | 350341 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7LY | LL137LY | ll13 7ly | ll137ly | Wrexham | Wrecsam | Abenbury WwTW | 3673 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333234 | 349971 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NA | LL137NA | ll13 7na | ll137na | Wrexham | Wrecsam | Abenbury WwTW | 3668 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333293 | 350079 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NB | LL137NB | ll13 7nb | ll137nb | Wrexham | Wrecsam | Abenbury WwTW | 3871 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333123 | 350193 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7ND | LL137ND | ll13 7nd | ll137nd | Wrexham | Wrecsam | Abenbury WwTW | 3690 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333166 | 349861 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NE | LL137NE | ll13 7ne | ll137ne | Wrexham | Wrecsam | Abenbury WwTW | 3832 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333164 | 350187 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NH | LL137NH | ll13 7nh | ll137nh | Wrexham | Wrecsam | Abenbury WwTW | 3973 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333000 | 350175 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NN | LL137NN | ll13 7nn | ll137nn | Wrexham | Wrecsam | Abenbury WwTW | 4011 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332990 | 350240 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NP | LL137NP | ll13 7np | ll137np | Wrexham | Wrecsam | Abenbury WwTW | 4013 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333014 | 350290 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NQ | LL137NQ | ll13 7nq | ll137nq | Wrexham | Wrecsam | Abenbury WwTW | 4307 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332803 | 350517 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NR | LL137NR | ll13 7nr | ll137nr | Wrexham | Wrecsam | Abenbury WwTW | 3929 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333063 | 350202 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NT | LL137NT | ll13 7nt | ll137nt | Wrexham | Wrecsam | Abenbury WwTW | 4471 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332521 | 350330 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NU | LL137NU | ll13 7nu | ll137nu | Wrexham | Wrecsam | Abenbury WwTW | 3717 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333140 | 349870 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NW | LL137NW | ll13 7nw | ll137nw | Wrexham | Wrecsam | Abenbury WwTW | 3961 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333053 | 350253 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NX | LL137NX | ll13 7nx | ll137nx | Wrexham | Wrecsam | Abenbury WwTW | 4155 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332848 | 350279 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NY | LL137NY | ll13 7ny | ll137ny | Wrexham | Wrecsam | Abenbury WwTW | 3613 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333238 | 349835 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7NZ | LL137NZ | ll13 7nz | ll137nz | Wrexham | Wrecsam | Abenbury WwTW | 4166 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332788 | 350182 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PB | LL137PB | ll13 7pb | ll137pb | Wrexham | Wrecsam | Abenbury WwTW | 3650 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333195 | 349828 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PD | LL137PD | ll13 7pd | ll137pd | Wrexham | Wrecsam | Abenbury WwTW | 3568 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333304 | 349872 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PE | LL137PE | ll13 7pe | ll137pe | Wrexham | Wrecsam | Abenbury WwTW | 3543 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333285 | 349766 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PF | LL137PF | ll13 7pf | ll137pf | Wrexham | Wrecsam | Abenbury WwTW | 3588 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333231 | 349752 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PG | LL137PG | ll13 7pg | ll137pg | Wrexham | Wrecsam | Abenbury WwTW | 3646 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333167 | 349749 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PH | LL137PH | ll13 7ph | ll137ph | Wrexham | Wrecsam | Abenbury WwTW | 3702 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333088 | 349699 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PL | LL137PL | ll13 7pl | ll137pl | Wrexham | Wrecsam | Abenbury WwTW | 3700 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333072 | 349649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PN | LL137PN | ll13 7pn | ll137pn | Wrexham | Wrecsam | Abenbury WwTW | 3611 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333186 | 349703 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PR | LL137PR | ll13 7pr | ll137pr | Wrexham | Wrecsam | Abenbury WwTW | 3656 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333085 | 349553 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PT | LL137PT | ll13 7pt | ll137pt | Wrexham | Wrecsam | Abenbury WwTW | 3577 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333203 | 349650 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PU | LL137PU | ll13 7pu | ll137pu | Wrexham | Wrecsam | Abenbury WwTW | 3820 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332924 | 349587 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PW | LL137PW | ll13 7pw | ll137pw | Wrexham | Wrecsam | Abenbury WwTW | 3673 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333089 | 349617 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7PY | LL137PY | ll13 7py | ll137py | Wrexham | Wrecsam | Abenbury WwTW | 3823 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332932 | 349622 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7QB | LL137QB | ll13 7qb | ll137qb | Wrexham | Wrecsam | Abenbury WwTW | 3372 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333216 | 348875 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7QD | LL137QD | ll13 7qd | ll137qd | Wrexham | Wrecsam | Abenbury WwTW | 3327 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333263 | 348881 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7QE | LL137QE | ll13 7qe | ll137qe | Wrexham | Wrecsam | Abenbury WwTW | 3499 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333127 | 349105 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7QF | LL137QF | ll13 7qf | ll137qf | Wrexham | Wrecsam | Abenbury WwTW | 3515 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333096 | 349028 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7QG | LL137QG | ll13 7qg | ll137qg | Wrexham | Wrecsam | Abenbury WwTW | 3465 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333145 | 349019 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7QH | LL137QH | ll13 7qh | ll137qh | Wrexham | Wrecsam | Abenbury WwTW | 3157 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333442 | 348929 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7QJ | LL137QJ | ll13 7qj | ll137qj | Wrexham | Wrecsam | Abenbury WwTW | 3132 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333452 | 348827 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7QL | LL137QL | ll13 7ql | ll137ql | Wrexham | Wrecsam | Abenbury WwTW | 3222 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333372 | 348905 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7QN | LL137QN | ll13 7qn | ll137qn | Wrexham | Wrecsam | Abenbury WwTW | 3267 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333347 | 349020 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7QP | LL137QP | ll13 7qp | ll137qp | Wrexham | Wrecsam | Abenbury WwTW | 3383 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333257 | 349157 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7QQ | LL137QQ | ll13 7qq | ll137qq | Wrexham | Wrecsam | Abenbury WwTW | 3384 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333249 | 349124 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7QW | LL137QW | ll13 7qw | ll137qw | Wrexham | Wrecsam | Abenbury WwTW | 3543 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 333055 | 348952 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RA | LL137RA | ll13 7ra | ll137ra | Wrexham | Wrecsam | Abenbury WwTW | 3880 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332862 | 349593 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RB | LL137RB | ll13 7rb | ll137rb | Wrexham | Wrecsam | Abenbury WwTW | 3914 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332808 | 349534 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RE | LL137RE | ll13 7re | ll137re | Wrexham | Wrecsam | Abenbury WwTW | 4000 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332715 | 349522 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RF | LL137RF | ll13 7rf | ll137rf | Wrexham | Wrecsam | Abenbury WwTW | 4193 | 813 | 700to900 | 1.63 | 1.19 | 0.87 | 15.15 | 8.08 | 8.93 | 332475 | 349366 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RH | LL137RH | ll13 7rh | ll137rh | Wrexham | Wrecsam | Abenbury WwTW | 3849 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 332865 | 349495 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RN | LL137RN | ll13 7rn | ll137rn | Wrexham | Wrecsam | Abenbury WwTW | 3853 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332872 | 349533 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RP | LL137RP | ll13 7rp | ll137rp | Wrexham | Wrecsam | Abenbury WwTW | 3849 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332976 | 349817 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RR | LL137RR | ll13 7rr | ll137rr | Wrexham | Wrecsam | Abenbury WwTW | 3881 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332967 | 349880 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RS | LL137RS | ll13 7rs | ll137rs | Wrexham | Wrecsam | Abenbury WwTW | 3873 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332924 | 349750 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RT | LL137RT | ll13 7rt | ll137rt | Wrexham | Wrecsam | Abenbury WwTW | 3712 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333109 | 349782 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RU | LL137RU | ll13 7ru | ll137ru | Wrexham | Wrecsam | Abenbury WwTW | 3801 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333001 | 349751 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RW | LL137RW | ll13 7rw | ll137rw | Wrexham | Wrecsam | Abenbury WwTW | 3920 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 332761 | 349386 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7RY | LL137RY | ll13 7ry | ll137ry | Wrexham | Wrecsam | Abenbury WwTW | 3767 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333032 | 349735 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SA | LL137SA | ll13 7sa | ll137sa | Wrexham | Wrecsam | Abenbury WwTW | 3845 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332929 | 349681 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SB | LL137SB | ll13 7sb | ll137sb | Wrexham | Wrecsam | Abenbury WwTW | 3787 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332984 | 349663 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SD | LL137SD | ll13 7sd | ll137sd | Wrexham | Wrecsam | Abenbury WwTW | 3843 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332942 | 349712 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SE | LL137SE | ll13 7se | ll137se | Wrexham | Wrecsam | Abenbury WwTW | 3943 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332873 | 349812 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SF | LL137SF | ll13 7sf | ll137sf | Wrexham | Wrecsam | Abenbury WwTW | 3978 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332862 | 349881 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SG | LL137SG | ll13 7sg | ll137sg | Wrexham | Wrecsam | Abenbury WwTW | 3916 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332899 | 349806 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SH | LL137SH | ll13 7sh | ll137sh | Wrexham | Wrecsam | Abenbury WwTW | 4063 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332759 | 349850 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SL | LL137SL | ll13 7sl | ll137sl | Wrexham | Wrecsam | Abenbury WwTW | 4049 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332764 | 349824 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SN | LL137SN | ll13 7sn | ll137sn | Wrexham | Wrecsam | Abenbury WwTW | 3725 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333007 | 349535 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SP | LL137SP | ll13 7sp | ll137sp | Wrexham | Wrecsam | Abenbury WwTW | 3572 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333269 | 349803 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SR | LL137SR | ll13 7sr | ll137sr | Wrexham | Wrecsam | Abenbury WwTW | 4136 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 333028 | 350562 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SU | LL137SU | ll13 7su | ll137su | Wrexham | Wrecsam | Abenbury WwTW | 4144 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332984 | 350504 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SX | LL137SX | ll13 7sx | ll137sx | Wrexham | Wrecsam | Abenbury WwTW | 4165 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332886 | 350373 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SY | LL137SY | ll13 7sy | ll137sy | Wrexham | Wrecsam | Abenbury WwTW | 4105 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332932 | 350331 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7SZ | LL137SZ | ll13 7sz | ll137sz | Wrexham | Wrecsam | Abenbury WwTW | 4204 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332860 | 350406 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TB | LL137TB | ll13 7tb | ll137tb | Wrexham | Wrecsam | Abenbury WwTW | 4224 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332809 | 350354 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TD | LL137TD | ll13 7td | ll137td | Wrexham | Wrecsam | Abenbury WwTW | 4471 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332521 | 350330 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TE | LL137TE | ll13 7te | ll137te | Wrexham | Wrecsam | Abenbury WwTW | 4329 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332695 | 350361 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TF | LL137TF | ll13 7tf | ll137tf | Wrexham | Wrecsam | Abenbury WwTW | 4265 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332739 | 350306 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TG | LL137TG | ll13 7tg | ll137tg | Wrexham | Wrecsam | Abenbury WwTW | 4048 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332952 | 350247 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TH | LL137TH | ll13 7th | ll137th | Wrexham | Wrecsam | Abenbury WwTW | 4106 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332904 | 350280 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TJ | LL137TJ | ll13 7tj | ll137tj | Wrexham | Wrecsam | Abenbury WwTW | 4459 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332577 | 350415 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TL | LL137TL | ll13 7tl | ll137tl | Wrexham | Wrecsam | Abenbury WwTW | 4074 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332923 | 350248 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TN | LL137TN | ll13 7tn | ll137tn | Wrexham | Wrecsam | Abenbury WwTW | 4114 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332877 | 350246 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TP | LL137TP | ll13 7tp | ll137tp | Wrexham | Wrecsam | Abenbury WwTW | 4042 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332884 | 350094 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TR | LL137TR | ll13 7tr | ll137tr | Wrexham | Wrecsam | Abenbury WwTW | 4091 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332848 | 350132 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TS | LL137TS | ll13 7ts | ll137ts | Wrexham | Wrecsam | Abenbury WwTW | 4109 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332803 | 350076 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TT | LL137TT | ll13 7tt | ll137tt | Wrexham | Wrecsam | Abenbury WwTW | 4029 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332857 | 350002 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TU | LL137TU | ll13 7tu | ll137tu | Wrexham | Wrecsam | Abenbury WwTW | 4140 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332751 | 350035 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TW | LL137TW | ll13 7tw | ll137tw | Wrexham | Wrecsam | Abenbury WwTW | 4103 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332852 | 350169 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TX | LL137TX | ll13 7tx | ll137tx | Wrexham | Wrecsam | Abenbury WwTW | 4591 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332514 | 350580 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TY | LL137TY | ll13 7ty | ll137ty | Wrexham | Wrecsam | Abenbury WwTW | 4428 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332483 | 350140 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7TZ | LL137TZ | ll13 7tz | ll137tz | Wrexham | Wrecsam | Abenbury WwTW | 4543 | 799 | 700to900 | 1.6 | 1.17 | 0.86 | 14.89 | 7.94 | 8.78 | 332533 | 350513 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UA | LL137UA | ll13 7ua | ll137ua | Wrexham | Wrecsam | Abenbury WwTW | 4369 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332493 | 350010 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UB | LL137UB | ll13 7ub | ll137ub | Wrexham | Wrecsam | Abenbury WwTW | 4562 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332287 | 350012 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UD | LL137UD | ll13 7ud | ll137ud | Wrexham | Wrecsam | Abenbury WwTW | 4421 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332416 | 349955 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UE | LL137UE | ll13 7ue | ll137ue | Wrexham | Wrecsam | Abenbury WwTW | 4345 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332474 | 349892 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UF | LL137UF | ll13 7uf | ll137uf | Wrexham | Wrecsam | Abenbury WwTW | 4354 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332425 | 349779 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UG | LL137UG | ll13 7ug | ll137ug | Wrexham | Wrecsam | Abenbury WwTW | 4032 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332740 | 349708 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UH | LL137UH | ll13 7uh | ll137uh | Wrexham | Wrecsam | Abenbury WwTW | 4151 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332627 | 349745 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UL | LL137UL | ll13 7ul | ll137ul | Wrexham | Wrecsam | Abenbury WwTW | 4380 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332391 | 349759 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UN | LL137UN | ll13 7un | ll137un | Wrexham | Wrecsam | Abenbury WwTW | 4011 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332785 | 349771 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UP | LL137UP | ll13 7up | ll137up | Wrexham | Wrecsam | Abenbury WwTW | 3940 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332832 | 349691 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UR | LL137UR | ll13 7ur | ll137ur | Wrexham | Wrecsam | Abenbury WwTW | 3965 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332842 | 349792 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7US | LL137US | ll13 7us | ll137us | Wrexham | Wrecsam | Abenbury WwTW | 3890 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332868 | 349643 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UT | LL137UT | ll13 7ut | ll137ut | Wrexham | Wrecsam | Abenbury WwTW | 3915 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332875 | 349739 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7UW | LL137UW | ll13 7uw | ll137uw | Wrexham | Wrecsam | Abenbury WwTW | 3925 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 332830 | 349639 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YD | LL137YD | ll13 7yd | ll137yd | Wrexham | Wrecsam | Abenbury WwTW | 2694 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334087 | 349482 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YE | LL137YE | ll13 7ye | ll137ye | Wrexham | Wrecsam | Abenbury WwTW | 3750 | 788 | 700to900 | 1.58 | 1.15 | 0.85 | 14.69 | 7.83 | 8.66 | 332878 | 349140 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YF | LL137YF | ll13 7yf | ll137yf | Wrexham | Wrecsam | Abenbury WwTW | 2883 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333941 | 349619 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YG | LL137YG | ll13 7yg | ll137yg | Wrexham | Wrecsam | Abenbury WwTW | 2766 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334039 | 349551 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YH | LL137YH | ll13 7yh | ll137yh | Wrexham | Wrecsam | Abenbury WwTW | 4904 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 332258 | 350764 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YJ | LL137YJ | ll13 7yj | ll137yj | Wrexham | Wrecsam | Abenbury WwTW | 2833 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333999 | 349624 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YL | LL137YL | ll13 7yl | ll137yl | Wrexham | Wrecsam | Abenbury WwTW | 4712 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 332473 | 350756 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YN | LL137YN | ll13 7yn | ll137yn | Wrexham | Wrecsam | Abenbury WwTW | 2883 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333960 | 349658 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YP | LL137YP | ll13 7yp | ll137yp | Wrexham | Wrecsam | Abenbury WwTW | 4986 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 332116 | 350671 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YQ | LL137YQ | ll13 7yq | ll137yq | Wrexham | Wrecsam | Abenbury WwTW | 2792 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334030 | 349595 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YR | LL137YR | ll13 7yr | ll137yr | Wrexham | Wrecsam | Abenbury WwTW | 3697 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333135 | 349806 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YS | LL137YS | ll13 7ys | ll137ys | Wrexham | Wrecsam | Abenbury WwTW | 2681 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334122 | 349529 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YT | LL137YT | ll13 7yt | ll137yt | Wrexham | Wrecsam | Abenbury WwTW | 4718 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 332409 | 350654 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YU | LL137YU | ll13 7yu | ll137yu | Wrexham | Wrecsam | Abenbury WwTW | 4818 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 332118 | 350278 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YW | LL137YW | ll13 7yw | ll137yw | Wrexham | Wrecsam | Abenbury WwTW | 4771 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 332364 | 350682 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7YX | LL137YX | ll13 7yx | ll137yx | Wrexham | Wrecsam | Abenbury WwTW | 4787 | 818 | 700to900 | 1.64 | 1.2 | 0.88 | 15.25 | 8.13 | 8.99 | 332329 | 350649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 7ZB | LL137ZB | ll13 7zb | ll137zb | Wrexham | Wrecsam | Abenbury WwTW | 5220 | 822 | 700to900 | 1.65 | 1.2 | 0.88 | 15.32 | 8.17 | 9.03 | 331738 | 350411 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8AD | LL138AD | ll13 8ad | ll138ad | Wrexham | Wrecsam | Abenbury WwTW | 3543 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333566 | 350305 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8AE | LL138AE | ll13 8ae | ll138ae | Wrexham | Wrecsam | Abenbury WwTW | 3573 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333562 | 350353 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8AF | LL138AF | ll13 8af | ll138af | Wrexham | Wrecsam | Abenbury WwTW | 2642 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334136 | 349466 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8AH | LL138AH | ll13 8ah | ll138ah | Wrexham | Wrecsam | Abenbury WwTW | 3588 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333619 | 350465 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8AP | LL138AP | ll13 8ap | ll138ap | Wrexham | Wrecsam | Abenbury WwTW | 2671 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334097 | 349448 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8AQ | LL138AQ | ll13 8aq | ll138aq | Wrexham | Wrecsam | Abenbury WwTW | 2357 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334622 | 349751 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8AZ | LL138AZ | ll13 8az | ll138az | Wrexham | Wrecsam | Abenbury WwTW | 3615 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333514 | 350357 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8BA | LL138BA | ll13 8ba | ll138ba | Wrexham | Wrecsam | Abenbury WwTW | 3492 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333639 | 350324 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8BB | LL138BB | ll13 8bb | ll138bb | Wrexham | Wrecsam | Abenbury WwTW | 3526 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333641 | 350388 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8BD | LL138BD | ll13 8bd | ll138bd | Wrexham | Wrecsam | Abenbury WwTW | 3487 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333620 | 350285 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8BE | LL138BE | ll13 8be | ll138be | Wrexham | Wrecsam | Abenbury WwTW | 3500 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333646 | 350349 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8BG | LL138BG | ll13 8bg | ll138bg | Wrexham | Wrecsam | Abenbury WwTW | 3620 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333596 | 350487 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8BS | LL138BS | ll13 8bs | ll138bs | Wrexham | Wrecsam | Abenbury WwTW | 3455 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333637 | 350252 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8BT | LL138BT | ll13 8bt | ll138bt | Wrexham | Wrecsam | Abenbury WwTW | 3399 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333706 | 350256 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8BX | LL138BX | ll13 8bx | ll138bx | Wrexham | Wrecsam | Abenbury WwTW | 3406 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333726 | 350299 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8BY | LL138BY | ll13 8by | ll138by | Wrexham | Wrecsam | Abenbury WwTW | 3412 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333744 | 350336 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DA | LL138DA | ll13 8da | ll138da | Wrexham | Wrecsam | Abenbury WwTW | 3387 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333793 | 350362 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DB | LL138DB | ll13 8db | ll138db | Wrexham | Wrecsam | Abenbury WwTW | 3337 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333780 | 350255 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DE | LL138DE | ll13 8de | ll138de | Wrexham | Wrecsam | Abenbury WwTW | 3339 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333908 | 350437 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DG | LL138DG | ll13 8dg | ll138dg | Wrexham | Wrecsam | Abenbury WwTW | 3242 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333820 | 350143 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DH | LL138DH | ll13 8dh | ll138dh | Wrexham | Wrecsam | Abenbury WwTW | 3521 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333682 | 350438 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DJ | LL138DJ | ll13 8dj | ll138dj | Wrexham | Wrecsam | Abenbury WwTW | 3313 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333729 | 350131 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DL | LL138DL | ll13 8dl | ll138dl | Wrexham | Wrecsam | Abenbury WwTW | 3176 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333803 | 349987 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DN | LL138DN | ll13 8dn | ll138dn | Wrexham | Wrecsam | Abenbury WwTW | 3373 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333644 | 350107 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DP | LL138DP | ll13 8dp | ll138dp | Wrexham | Wrecsam | Abenbury WwTW | 3350 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333719 | 350185 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DQ | LL138DQ | ll13 8dq | ll138dq | Wrexham | Wrecsam | Abenbury WwTW | 2797 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334172 | 349868 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DS | LL138DS | ll13 8ds | ll138ds | Wrexham | Wrecsam | Abenbury WwTW | 3153 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333856 | 350032 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DT | LL138DT | ll13 8dt | ll138dt | Wrexham | Wrecsam | Abenbury WwTW | 2991 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333966 | 349901 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DU | LL138DU | ll13 8du | ll138du | Wrexham | Wrecsam | Abenbury WwTW | 2870 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334082 | 349859 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DW | LL138DW | ll13 8dw | ll138dw | Wrexham | Wrecsam | Abenbury WwTW | 3327 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333672 | 350063 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DX | LL138DX | ll13 8dx | ll138dx | Wrexham | Wrecsam | Abenbury WwTW | 3119 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333795 | 349855 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DY | LL138DY | ll13 8dy | ll138dy | Wrexham | Wrecsam | Abenbury WwTW | 2875 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334087 | 349877 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8DZ | LL138DZ | ll13 8dz | ll138dz | Wrexham | Wrecsam | Abenbury WwTW | 3103 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333891 | 349994 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EA | LL138EA | ll13 8ea | ll138ea | Wrexham | Wrecsam | Abenbury WwTW | 2883 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334019 | 349775 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EB | LL138EB | ll13 8eb | ll138eb | Wrexham | Wrecsam | Abenbury WwTW | 3056 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333989 | 350062 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8ED | LL138ED | ll13 8ed | ll138ed | Wrexham | Wrecsam | Abenbury WwTW | 2947 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334018 | 349902 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EE | LL138EE | ll13 8ee | ll138ee | Wrexham | Wrecsam | Abenbury WwTW | 2941 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334089 | 350005 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EF | LL138EF | ll13 8ef | ll138ef | Wrexham | Wrecsam | Abenbury WwTW | 2931 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334144 | 350069 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EG | LL138EG | ll13 8eg | ll138eg | Wrexham | Wrecsam | Abenbury WwTW | 2824 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334282 | 350078 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EH | LL138EH | ll13 8eh | ll138eh | Wrexham | Wrecsam | Abenbury WwTW | 2889 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334180 | 350047 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EJ | LL138EJ | ll13 8ej | ll138ej | Wrexham | Wrecsam | Abenbury WwTW | 2797 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334236 | 349966 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EL | LL138EL | ll13 8el | ll138el | Wrexham | Wrecsam | Abenbury WwTW | 2871 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334210 | 350059 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EN | LL138EN | ll13 8en | ll138en | Wrexham | Wrecsam | Abenbury WwTW | 3082 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334031 | 350171 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EP | LL138EP | ll13 8ep | ll138ep | Wrexham | Wrecsam | Abenbury WwTW | 3004 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334091 | 350121 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EQ | LL138EQ | ll13 8eq | ll138eq | Wrexham | Wrecsam | Abenbury WwTW | 3116 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333818 | 349892 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8ER | LL138ER | ll13 8er | ll138er | Wrexham | Wrecsam | Abenbury WwTW | 2950 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334169 | 350137 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8ES | LL138ES | ll13 8es | ll138es | Wrexham | Wrecsam | Abenbury WwTW | 2899 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334245 | 350154 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8ET | LL138ET | ll13 8et | ll138et | Wrexham | Wrecsam | Abenbury WwTW | 2999 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334228 | 350294 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EU | LL138EU | ll13 8eu | ll138eu | Wrexham | Wrecsam | Abenbury WwTW | 2997 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334177 | 350227 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EW | LL138EW | ll13 8ew | ll138ew | Wrexham | Wrecsam | Abenbury WwTW | 2728 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334221 | 349815 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8EY | LL138EY | ll13 8ey | ll138ey | Wrexham | Wrecsam | Abenbury WwTW | 3013 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334143 | 350209 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8HA | LL138HA | ll13 8ha | ll138ha | Wrexham | Wrecsam | Abenbury WwTW | 3080 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334058 | 350206 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8HB | LL138HB | ll13 8hb | ll138hb | Wrexham | Wrecsam | Abenbury WwTW | 3080 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334107 | 350272 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8HD | LL138HD | ll13 8hd | ll138hd | Wrexham | Wrecsam | Abenbury WwTW | 3164 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334017 | 350292 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8HE | LL138HE | ll13 8he | ll138he | Wrexham | Wrecsam | Abenbury WwTW | 3105 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334029 | 350209 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8HF | LL138HF | ll13 8hf | ll138hf | Wrexham | Wrecsam | Abenbury WwTW | 3281 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333897 | 350326 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8HH | LL138HH | ll13 8hh | ll138hh | Wrexham | Wrecsam | Abenbury WwTW | 3110 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334198 | 350431 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8HL | LL138HL | ll13 8hl | ll138hl | Wrexham | Wrecsam | Abenbury WwTW | 3466 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334003 | 350747 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8HN | LL138HN | ll13 8hn | ll138hn | Wrexham | Wrecsam | Abenbury WwTW | 3393 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334134 | 350779 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8HP | LL138HP | ll13 8hp | ll138hp | Wrexham | Wrecsam | Abenbury WwTW | 3503 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333569 | 350233 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8HR | LL138HR | ll13 8hr | ll138hr | Wrexham | Wrecsam | Abenbury WwTW | 3467 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333583 | 350187 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8HY | LL138HY | ll13 8hy | ll138hy | Wrexham | Wrecsam | Abenbury WwTW | 3495 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333560 | 350204 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8JA | LL138JA | ll13 8ja | ll138ja | Wrexham | Wrecsam | Abenbury WwTW | 1558 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335195 | 349163 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8JB | LL138JB | ll13 8jb | ll138jb | Wrexham | Wrecsam | Abenbury WwTW | 1475 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335293 | 349168 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8JD | LL138JD | ll13 8jd | ll138jd | Wrexham | Wrecsam | Abenbury WwTW | 1500 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335223 | 349093 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8JE | LL138JE | ll13 8je | ll138je | Wrexham | Wrecsam | Abenbury WwTW | 1437 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335311 | 349123 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8JF | LL138JF | ll13 8jf | ll138jf | Wrexham | Wrecsam | Abenbury WwTW | 1418 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335299 | 349063 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8JG | LL138JG | ll13 8jg | ll138jg | Wrexham | Wrecsam | Abenbury WwTW | 1501 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335205 | 349060 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8JH | LL138JH | ll13 8jh | ll138jh | Wrexham | Wrecsam | Abenbury WwTW | 1465 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335252 | 349074 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8JJ | LL138JJ | ll13 8jj | ll138jj | Wrexham | Wrecsam | Abenbury WwTW | 1541 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335143 | 349022 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8JL | LL138JL | ll13 8jl | ll138jl | Wrexham | Wrecsam | Abenbury WwTW | 1495 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335173 | 348975 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8JQ | LL138JQ | ll13 8jq | ll138jq | Wrexham | Wrecsam | Abenbury WwTW | 1395 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335318 | 349049 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8LP | LL138LP | ll13 8lp | ll138lp | Wrexham | Wrecsam | Abenbury WwTW | 3439 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333641 | 350228 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8LS | LL138LS | ll13 8ls | ll138ls | Wrexham | Wrecsam | Abenbury WwTW | 3518 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333515 | 350173 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8LU | LL138LU | ll13 8lu | ll138lu | Wrexham | Wrecsam | Abenbury WwTW | 3559 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333463 | 350164 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8LW | LL138LW | ll13 8lw | ll138lw | Wrexham | Wrecsam | Abenbury WwTW | 3416 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333635 | 350175 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8LY | LL138LY | ll13 8ly | ll138ly | Wrexham | Wrecsam | Abenbury WwTW | 3501 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333538 | 350179 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NA | LL138NA | ll13 8na | ll138na | Wrexham | Wrecsam | Abenbury WwTW | 3564 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333466 | 350180 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NB | LL138NB | ll13 8nb | ll138nb | Wrexham | Wrecsam | Abenbury WwTW | 3584 | 791 | 700to900 | 1.58 | 1.16 | 0.85 | 14.74 | 7.86 | 8.69 | 333449 | 350190 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NE | LL138NE | ll13 8ne | ll138ne | Wrexham | Wrecsam | Abenbury WwTW | 3401 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334112 | 350768 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NF | LL138NF | ll13 8nf | ll138nf | Wrexham | Wrecsam | Abenbury WwTW | 3327 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334287 | 350837 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NG | LL138NG | ll13 8ng | ll138ng | Wrexham | Wrecsam | Abenbury WwTW | 3285 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334393 | 350875 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NH | LL138NH | ll13 8nh | ll138nh | Wrexham | Wrecsam | Abenbury WwTW | 3068 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333804 | 349760 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NL | LL138NL | ll13 8nl | ll138nl | Wrexham | Wrecsam | Abenbury WwTW | 2962 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333906 | 349728 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NN | LL138NN | ll13 8nn | ll138nn | Wrexham | Wrecsam | Abenbury WwTW | 2790 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334063 | 349657 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NR | LL138NR | ll13 8nr | ll138nr | Wrexham | Wrecsam | Abenbury WwTW | 2407 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334321 | 349299 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NS | LL138NS | ll13 8ns | ll138ns | Wrexham | Wrecsam | Abenbury WwTW | 3075 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333820 | 349809 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NT | LL138NT | ll13 8nt | ll138nt | Wrexham | Wrecsam | Abenbury WwTW | 2991 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333900 | 349781 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NU | LL138NU | ll13 8nu | ll138nu | Wrexham | Wrecsam | Abenbury WwTW | 2958 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333933 | 349771 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NW | LL138NW | ll13 8nw | ll138nw | Wrexham | Wrecsam | Abenbury WwTW | 2563 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334228 | 349478 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NX | LL138NX | ll13 8nx | ll138nx | Wrexham | Wrecsam | Abenbury WwTW | 2425 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334342 | 349394 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8NY | LL138NY | ll13 8ny | ll138ny | Wrexham | Wrecsam | Abenbury WwTW | 3045 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333858 | 349816 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PA | LL138PA | ll13 8pa | ll138pa | Wrexham | Wrecsam | Abenbury WwTW | 2925 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333981 | 349793 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PE | LL138PE | ll13 8pe | ll138pe | Wrexham | Wrecsam | Abenbury WwTW | 2723 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334171 | 349718 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PF | LL138PF | ll13 8pf | ll138pf | Wrexham | Wrecsam | Abenbury WwTW | 2663 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334214 | 349673 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PG | LL138PG | ll13 8pg | ll138pg | Wrexham | Wrecsam | Abenbury WwTW | 2717 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334136 | 349639 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PH | LL138PH | ll13 8ph | ll138ph | Wrexham | Wrecsam | Abenbury WwTW | 2789 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334107 | 349739 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PL | LL138PL | ll13 8pl | ll138pl | Wrexham | Wrecsam | Abenbury WwTW | 2646 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334270 | 349737 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PN | LL138PN | ll13 8pn | ll138pn | Wrexham | Wrecsam | Abenbury WwTW | 2517 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334297 | 349515 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PP | LL138PP | ll13 8pp | ll138pp | Wrexham | Wrecsam | Abenbury WwTW | 2471 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334392 | 349597 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PR | LL138PR | ll13 8pr | ll138pr | Wrexham | Wrecsam | Abenbury WwTW | 2532 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334308 | 349570 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PS | LL138PS | ll13 8ps | ll138ps | Wrexham | Wrecsam | Abenbury WwTW | 2407 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334432 | 349537 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PT | LL138PT | ll13 8pt | ll138pt | Wrexham | Wrecsam | Abenbury WwTW | 2475 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334420 | 349654 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PU | LL138PU | ll13 8pu | ll138pu | Wrexham | Wrecsam | Abenbury WwTW | 2549 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334366 | 349709 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PW | LL138PW | ll13 8pw | ll138pw | Wrexham | Wrecsam | Abenbury WwTW | 2540 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334343 | 349652 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8PY | LL138PY | ll13 8py | ll138py | Wrexham | Wrecsam | Abenbury WwTW | 2446 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334455 | 349658 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QA | LL138QA | ll13 8qa | ll138qa | Wrexham | Wrecsam | Abenbury WwTW | 2660 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334165 | 349571 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QH | LL138QH | ll13 8qh | ll138qh | Wrexham | Wrecsam | Abenbury WwTW | 2315 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334397 | 349241 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QJ | LL138QJ | ll13 8qj | ll138qj | Wrexham | Wrecsam | Abenbury WwTW | 2542 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334139 | 349195 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QL | LL138QL | ll13 8ql | ll138ql | Wrexham | Wrecsam | Abenbury WwTW | 2605 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334069 | 349182 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QN | LL138QN | ll13 8qn | ll138qn | Wrexham | Wrecsam | Abenbury WwTW | 2521 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334134 | 349108 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QP | LL138QP | ll13 8qp | ll138qp | Wrexham | Wrecsam | Abenbury WwTW | 2432 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334237 | 349140 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QR | LL138QR | ll13 8qr | ll138qr | Wrexham | Wrecsam | Abenbury WwTW | 2480 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334252 | 349324 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QS | LL138QS | ll13 8qs | ll138qs | Wrexham | Wrecsam | Abenbury WwTW | 2451 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334258 | 349259 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QT | LL138QT | ll13 8qt | ll138qt | Wrexham | Wrecsam | Abenbury WwTW | 2352 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334325 | 349150 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QU | LL138QU | ll13 8qu | ll138qu | Wrexham | Wrecsam | Abenbury WwTW | 2491 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334197 | 349207 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QW | LL138QW | ll13 8qw | ll138qw | Wrexham | Wrecsam | Abenbury WwTW | 2467 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334204 | 349150 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QX | LL138QX | ll13 8qx | ll138qx | Wrexham | Wrecsam | Abenbury WwTW | 2480 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334224 | 349251 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QY | LL138QY | ll13 8qy | ll138qy | Wrexham | Wrecsam | Abenbury WwTW | 2509 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334211 | 349299 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8QZ | LL138QZ | ll13 8qz | ll138qz | Wrexham | Wrecsam | Abenbury WwTW | 2528 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334228 | 349392 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RA | LL138RA | ll13 8ra | ll138ra | Wrexham | Wrecsam | Abenbury WwTW | 2320 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334535 | 349544 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RB | LL138RB | ll13 8rb | ll138rb | Wrexham | Wrecsam | Abenbury WwTW | 2634 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334230 | 349640 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RD | LL138RD | ll13 8rd | ll138rd | Wrexham | Wrecsam | Abenbury WwTW | 2587 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334123 | 349285 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RE | LL138RE | ll13 8re | ll138re | Wrexham | Wrecsam | Abenbury WwTW | 2624 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334139 | 349428 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RF | LL138RF | ll13 8rf | ll138rf | Wrexham | Wrecsam | Abenbury WwTW | 2680 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334078 | 349425 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RG | LL138RG | ll13 8rg | ll138rg | Wrexham | Wrecsam | Abenbury WwTW | 3351 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334119 | 350704 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RH | LL138RH | ll13 8rh | ll138rh | Wrexham | Wrecsam | Abenbury WwTW | 3279 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334322 | 350804 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RJ | LL138RJ | ll13 8rj | ll138rj | Wrexham | Wrecsam | Abenbury WwTW | 2598 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334182 | 349460 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RL | LL138RL | ll13 8rl | ll138rl | Wrexham | Wrecsam | Abenbury WwTW | 3232 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334453 | 350857 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RN | LL138RN | ll13 8rn | ll138rn | Wrexham | Wrecsam | Abenbury WwTW | 3284 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334251 | 350742 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RP | LL138RP | ll13 8rp | ll138rp | Wrexham | Wrecsam | Abenbury WwTW | 3084 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334434 | 350642 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RQ | LL138RQ | ll13 8rq | ll138rq | Wrexham | Wrecsam | Abenbury WwTW | 2728 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334033 | 349443 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RR | LL138RR | ll13 8rr | ll138rr | Wrexham | Wrecsam | Abenbury WwTW | 3173 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334332 | 350667 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RS | LL138RS | ll13 8rs | ll138rs | Wrexham | Wrecsam | Abenbury WwTW | 3165 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334382 | 350703 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RT | LL138RT | ll13 8rt | ll138rt | Wrexham | Wrecsam | Abenbury WwTW | 3230 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334385 | 350795 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RU | LL138RU | ll13 8ru | ll138ru | Wrexham | Wrecsam | Abenbury WwTW | 3156 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334501 | 350799 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RW | LL138RW | ll13 8rw | ll138rw | Wrexham | Wrecsam | Abenbury WwTW | 3261 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334302 | 350760 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RX | LL138RX | ll13 8rx | ll138rx | Wrexham | Wrecsam | Abenbury WwTW | 2725 | 766 | 700to900 | 1.53 | 1.12 | 0.82 | 14.28 | 7.61 | 8.42 | 334020 | 349402 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8RY | LL138RY | ll13 8ry | ll138ry | Wrexham | Wrecsam | Abenbury WwTW | 3089 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334523 | 350729 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SA | LL138SA | ll13 8sa | ll138sa | Wrexham | Wrecsam | Abenbury WwTW | 3072 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334562 | 350740 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SB | LL138SB | ll13 8sb | ll138sb | Wrexham | Wrecsam | Abenbury WwTW | 3019 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334622 | 350722 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SD | LL138SD | ll13 8sd | ll138sd | Wrexham | Wrecsam | Abenbury WwTW | 3041 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334589 | 350722 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SE | LL138SE | ll13 8se | ll138se | Wrexham | Wrecsam | Abenbury WwTW | 3007 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334539 | 350633 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SF | LL138SF | ll13 8sf | ll138sf | Wrexham | Wrecsam | Abenbury WwTW | 2990 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334503 | 350577 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SG | LL138SG | ll13 8sg | ll138sg | Wrexham | Wrecsam | Abenbury WwTW | 3013 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334468 | 350576 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SH | LL138SH | ll13 8sh | ll138sh | Wrexham | Wrecsam | Abenbury WwTW | 2969 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334453 | 350500 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SJ | LL138SJ | ll13 8sj | ll138sj | Wrexham | Wrecsam | Abenbury WwTW | 2557 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334426 | 349819 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SL | LL138SL | ll13 8sl | ll138sl | Wrexham | Wrecsam | Abenbury WwTW | 3006 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334365 | 350461 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SN | LL138SN | ll13 8sn | ll138sn | Wrexham | Wrecsam | Abenbury WwTW | 2831 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334458 | 350305 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SP | LL138SP | ll13 8sp | ll138sp | Wrexham | Wrecsam | Abenbury WwTW | 3147 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334251 | 350546 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SQ | LL138SQ | ll13 8sq | ll138sq | Wrexham | Wrecsam | Abenbury WwTW | 2585 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334430 | 349875 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SR | LL138SR | ll13 8sr | ll138sr | Wrexham | Wrecsam | Abenbury WwTW | 2966 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334272 | 350296 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SS | LL138SS | ll13 8ss | ll138ss | Wrexham | Wrecsam | Abenbury WwTW | 2919 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334297 | 350252 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8ST | LL138ST | ll13 8st | ll138st | Wrexham | Wrecsam | Abenbury WwTW | 3066 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334244 | 350418 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SU | LL138SU | ll13 8su | ll138su | Wrexham | Wrecsam | Abenbury WwTW | 3145 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334214 | 350502 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SW | LL138SW | ll13 8sw | ll138sw | Wrexham | Wrecsam | Abenbury WwTW | 3095 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334298 | 350521 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SX | LL138SX | ll13 8sx | ll138sx | Wrexham | Wrecsam | Abenbury WwTW | 2652 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334346 | 349871 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8SY | LL138SY | ll13 8sy | ll138sy | Wrexham | Wrecsam | Abenbury WwTW | 3219 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334172 | 350567 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TA | LL138TA | ll13 8ta | ll138ta | Wrexham | Wrecsam | Abenbury WwTW | 3271 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334151 | 350620 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TB | LL138TB | ll13 8tb | ll138tb | Wrexham | Wrecsam | Abenbury WwTW | 3319 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334208 | 350749 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TD | LL138TD | ll13 8td | ll138td | Wrexham | Wrecsam | Abenbury WwTW | 3110 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 334459 | 350700 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TE | LL138TE | ll13 8te | ll138te | Wrexham | Wrecsam | Abenbury WwTW | 2877 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334342 | 350241 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TG | LL138TG | ll13 8tg | ll138tg | Wrexham | Wrecsam | Abenbury WwTW | 2148 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334928 | 349805 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TH | LL138TH | ll13 8th | ll138th | Wrexham | Wrecsam | Abenbury WwTW | 2448 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334968 | 350266 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TJ | LL138TJ | ll13 8tj | ll138tj | Wrexham | Wrecsam | Abenbury WwTW | 3643 | 774 | 700to900 | 1.55 | 1.13 | 0.83 | 14.43 | 7.69 | 8.5 | 333595 | 350526 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TL | LL138TL | ll13 8tl | ll138tl | Wrexham | Wrecsam | Abenbury WwTW | 2333 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335027 | 350166 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TN | LL138TN | ll13 8tn | ll138tn | Wrexham | Wrecsam | Abenbury WwTW | 2256 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334894 | 349930 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TP | LL138TP | ll13 8tp | ll138tp | Wrexham | Wrecsam | Abenbury WwTW | 2425 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334791 | 350067 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TR | LL138TR | ll13 8tr | ll138tr | Wrexham | Wrecsam | Abenbury WwTW | 2347 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334888 | 350055 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TS | LL138TS | ll13 8ts | ll138ts | Wrexham | Wrecsam | Abenbury WwTW | 1962 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335126 | 349747 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TT | LL138TT | ll13 8tt | ll138tt | Wrexham | Wrecsam | Abenbury WwTW | 2115 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335007 | 349844 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TU | LL138TU | ll13 8tu | ll138tu | Wrexham | Wrecsam | Abenbury WwTW | 2235 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334844 | 349841 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TW | LL138TW | ll13 8tw | ll138tw | Wrexham | Wrecsam | Abenbury WwTW | 2409 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334758 | 350008 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8TY | LL138TY | ll13 8ty | ll138ty | Wrexham | Wrecsam | Abenbury WwTW | 2207 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334805 | 349747 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UA | LL138UA | ll13 8ua | ll138ua | Wrexham | Wrecsam | Abenbury WwTW | 2344 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334699 | 349835 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UB | LL138UB | ll13 8ub | ll138ub | Wrexham | Wrecsam | Abenbury WwTW | 2353 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334727 | 349884 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UD | LL138UD | ll13 8ud | ll138ud | Wrexham | Wrecsam | Abenbury WwTW | 2481 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334585 | 349911 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UG | LL138UG | ll13 8ug | ll138ug | Wrexham | Wrecsam | Abenbury WwTW | 2272 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334634 | 349617 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UH | LL138UH | ll13 8uh | ll138uh | Wrexham | Wrecsam | Abenbury WwTW | 2751 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334477 | 350206 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UL | LL138UL | ll13 8ul | ll138ul | Wrexham | Wrecsam | Abenbury WwTW | 2540 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334500 | 349895 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UN | LL138UN | ll13 8un | ll138un | Wrexham | Wrecsam | Abenbury WwTW | 2323 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334669 | 349759 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UQ | LL138UQ | ll13 8uq | ll138uq | Wrexham | Wrecsam | Abenbury WwTW | 2909 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 333961 | 349720 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UR | LL138UR | ll13 8ur | ll138ur | Wrexham | Wrecsam | Abenbury WwTW | 2613 | 768 | 700to900 | 1.54 | 1.12 | 0.82 | 14.31 | 7.63 | 8.44 | 334431 | 349924 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8US | LL138US | ll13 8us | ll138us | Wrexham | Wrecsam | Abenbury WwTW | 2480 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334530 | 349834 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UT | LL138UT | ll13 8ut | ll138ut | Wrexham | Wrecsam | Abenbury WwTW | 2444 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334556 | 349809 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UU | LL138UU | ll13 8uu | ll138uu | Wrexham | Wrecsam | Abenbury WwTW | 2095 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334918 | 349710 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UW | LL138UW | ll13 8uw | ll138uw | Wrexham | Wrecsam | Abenbury WwTW | 1929 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334983 | 349521 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8UY | LL138UY | ll13 8uy | ll138uy | Wrexham | Wrecsam | Abenbury WwTW | 2010 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334998 | 349674 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8YA | LL138YA | ll13 8ya | ll138ya | Wrexham | Wrecsam | Abenbury WwTW | 2013 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335038 | 349727 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8YB | LL138YB | ll13 8yb | ll138yb | Wrexham | Wrecsam | Abenbury WwTW | 2134 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334911 | 349764 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8YD | LL138YD | ll13 8yd | ll138yd | Wrexham | Wrecsam | Abenbury WwTW | 1682 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335264 | 349482 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8YE | LL138YE | ll13 8ye | ll138ye | Wrexham | Wrecsam | Abenbury WwTW | 1511 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335405 | 349383 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8YF | LL138YF | ll13 8yf | ll138yf | Wrexham | Wrecsam | Abenbury WwTW | 1514 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335316 | 349274 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8YG | LL138YG | ll13 8yg | ll138yg | Wrexham | Wrecsam | Abenbury WwTW | 1633 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335257 | 349395 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8YH | LL138YH | ll13 8yh | ll138yh | Wrexham | Wrecsam | Abenbury WwTW | 1624 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335165 | 349244 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8YL | LL138YL | ll13 8yl | ll138yl | Wrexham | Wrecsam | Abenbury WwTW | 1688 | 743 | 700to900 | 1.49 | 1.09 | 0.8 | 13.85 | 7.39 | 8.16 | 335163 | 349358 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 8YR | LL138YR | ll13 8yr | ll138yr | Wrexham | Wrecsam | Abenbury WwTW | 2085 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334820 | 349560 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AB | LL139AB | ll13 9ab | ll139ab | Wrexham | Wrecsam | Abenbury WwTW | 2701 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335132 | 350698 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AD | LL139AD | ll13 9ad | ll139ad | Wrexham | Wrecsam | Isycoed Marshlea STW | 2776 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 337317 | 352018 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AE | LL139AE | ll13 9ae | ll139ae | Wrexham | Wrecsam | Abenbury WwTW | 734 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 336939 | 349028 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AF | LL139AF | ll13 9af | ll139af | Wrexham | Wrecsam | Gresford STW | 3780 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335243 | 352019 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AG | LL139AG | ll13 9ag | ll139ag | Wrexham | Wrecsam | Abenbury WwTW | 2791 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335000 | 350720 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AH | LL139AH | ll13 9ah | ll139ah | Wrexham | Wrecsam | Holt STW | 1090 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340756 | 353767 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AJ | LL139AJ | ll13 9aj | ll139aj | Wrexham | Wrecsam | Holt STW | 1163 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340883 | 353735 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AL | LL139AL | ll13 9al | ll139al | Wrexham | Wrecsam | Holt STW | 1109 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341190 | 353993 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AN | LL139AN | ll13 9an | ll139an | Wrexham | Wrecsam | Abenbury WwTW | 3162 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334913 | 351104 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AP | LL139AP | ll13 9ap | ll139ap | Wrexham | Wrecsam | Abenbury WwTW | 3185 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334573 | 350895 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AQ | LL139AQ | ll13 9aq | ll139aq | Wrexham | Wrecsam | Holt STW | 1177 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340758 | 353677 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AR | LL139AR | ll13 9ar | ll139ar | Wrexham | Wrecsam | Abenbury WwTW | 3120 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334618 | 350848 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AS | LL139AS | ll13 9as | ll139as | Wrexham | Wrecsam | Abenbury WwTW | 2926 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334834 | 350769 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AT | LL139AT | ll13 9at | ll139at | Wrexham | Wrecsam | Abenbury WwTW | 2632 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335173 | 350643 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AU | LL139AU | ll13 9au | ll139au | Wrexham | Wrecsam | Abenbury WwTW | 3145 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334678 | 350926 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AW | LL139AW | ll13 9aw | ll139aw | Wrexham | Wrecsam | Abenbury WwTW | 2375 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335218 | 350366 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AX | LL139AX | ll13 9ax | ll139ax | Wrexham | Wrecsam | Holt STW | 1192 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341142 | 353847 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AY | LL139AY | ll13 9ay | ll139ay | Wrexham | Wrecsam | Abenbury WwTW | 3090 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334803 | 350948 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9AZ | LL139AZ | ll13 9az | ll139az | Wrexham | Wrecsam | Holt STW | 1237 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341064 | 353742 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BA | LL139BA | ll13 9ba | ll139ba | Wrexham | Wrecsam | Abenbury WwTW | 2838 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334863 | 350681 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BB | LL139BB | ll13 9bb | ll139bb | Wrexham | Wrecsam | Abenbury WwTW | 2926 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334798 | 350742 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BD | LL139BD | ll13 9bd | ll139bd | Wrexham | Wrecsam | Abenbury WwTW | 2738 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334938 | 350612 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BE | LL139BE | ll13 9be | ll139be | Wrexham | Wrecsam | Abenbury WwTW | 2773 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334777 | 350530 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BF | LL139BF | ll13 9bf | ll139bf | Wrexham | Wrecsam | Abenbury WwTW | 2125 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335090 | 349942 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BG | LL139BG | ll13 9bg | ll139bg | Wrexham | Wrecsam | Abenbury WwTW | 2704 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334870 | 350518 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BH | LL139BH | ll13 9bh | ll139bh | Wrexham | Wrecsam | Abenbury WwTW | 2626 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335071 | 350569 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BJ | LL139BJ | ll13 9bj | ll139bj | Wrexham | Wrecsam | Holt STW | 1140 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340939 | 353786 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BL | LL139BL | ll13 9bl | ll139bl | Wrexham | Wrecsam | Abenbury WwTW | 2528 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335205 | 350540 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BN | LL139BN | ll13 9bn | ll139bn | Wrexham | Wrecsam | Abenbury WwTW | 2641 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335126 | 350624 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BP | LL139BP | ll13 9bp | ll139bp | Wrexham | Wrecsam | Abenbury WwTW | 2644 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334991 | 350535 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BQ | LL139BQ | ll13 9bq | ll139bq | Wrexham | Wrecsam | Abenbury WwTW | 1867 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335338 | 349819 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BS | LL139BS | ll13 9bs | ll139bs | Wrexham | Wrecsam | Abenbury WwTW | 2816 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334895 | 350677 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BT | LL139BT | ll13 9bt | ll139bt | Wrexham | Wrecsam | Abenbury WwTW | 2965 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334641 | 350667 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BU | LL139BU | ll13 9bu | ll139bu | Wrexham | Wrecsam | Abenbury WwTW | 2898 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334911 | 350789 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BW | LL139BW | ll13 9bw | ll139bw | Wrexham | Wrecsam | Abenbury WwTW | 2562 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335237 | 350600 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BX | LL139BX | ll13 9bx | ll139bx | Wrexham | Wrecsam | Abenbury WwTW | 3156 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335166 | 351236 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9BY | LL139BY | ll13 9by | ll139by | Wrexham | Wrecsam | Abenbury WwTW | 2917 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334963 | 350847 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DA | LL139DA | ll13 9da | ll139da | Wrexham | Wrecsam | Abenbury WwTW | 2938 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334998 | 350894 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DB | LL139DB | ll13 9db | ll139db | Wrexham | Wrecsam | Abenbury WwTW | 2956 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335050 | 350947 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DD | LL139DD | ll13 9dd | ll139dd | Wrexham | Wrecsam | Abenbury WwTW | 2978 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335089 | 350995 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DE | LL139DE | ll13 9de | ll139de | Wrexham | Wrecsam | Abenbury WwTW | 3084 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335103 | 351123 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DF | LL139DF | ll13 9df | ll139df | Wrexham | Wrecsam | Abenbury WwTW | 2893 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335001 | 350843 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DG | LL139DG | ll13 9dg | ll139dg | Wrexham | Wrecsam | Abenbury WwTW | 2942 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335122 | 350972 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DH | LL139DH | ll13 9dh | ll139dh | Wrexham | Wrecsam | Abenbury WwTW | 3023 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335156 | 351082 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DJ | LL139DJ | ll13 9dj | ll139dj | Wrexham | Wrecsam | Holt STW | 1058 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340930 | 353873 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DL | LL139DL | ll13 9dl | ll139dl | Wrexham | Wrecsam | Abenbury WwTW | 2953 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334910 | 350855 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DN | LL139DN | ll13 9dn | ll139dn | Wrexham | Wrecsam | Abenbury WwTW | 2970 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334963 | 350910 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DP | LL139DP | ll13 9dp | ll139dp | Wrexham | Wrecsam | Abenbury WwTW | 3020 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335044 | 351017 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DQ | LL139DQ | ll13 9dq | ll139dq | Wrexham | Wrecsam | Abenbury WwTW | 3520 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335745 | 351827 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DR | LL139DR | ll13 9dr | ll139dr | Wrexham | Wrecsam | Abenbury WwTW | 3040 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334934 | 350974 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DS | LL139DS | ll13 9ds | ll139ds | Wrexham | Wrecsam | Abenbury WwTW | 2887 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335144 | 350921 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DT | LL139DT | ll13 9dt | ll139dt | Wrexham | Wrecsam | Abenbury WwTW | 2917 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335174 | 350972 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DU | LL139DU | ll13 9du | ll139du | Wrexham | Wrecsam | Abenbury WwTW | 3038 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335060 | 351047 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DW | LL139DW | ll13 9dw | ll139dw | Wrexham | Wrecsam | Abenbury WwTW | 2990 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335004 | 350959 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DX | LL139DX | ll13 9dx | ll139dx | Wrexham | Wrecsam | Abenbury WwTW | 3091 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334913 | 351021 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DY | LL139DY | ll13 9dy | ll139dy | Wrexham | Wrecsam | Abenbury WwTW | 3167 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334964 | 351141 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9DZ | LL139DZ | ll13 9dz | ll139dz | Wrexham | Wrecsam | Abenbury WwTW | 3177 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335311 | 351325 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EA | LL139EA | ll13 9ea | ll139ea | Wrexham | Wrecsam | Abenbury WwTW | 3230 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335120 | 351296 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EB | LL139EB | ll13 9eb | ll139eb | Wrexham | Wrecsam | Abenbury WwTW | 3119 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335020 | 351118 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9ED | LL139ED | ll13 9ed | ll139ed | Wrexham | Wrecsam | Abenbury WwTW | 3164 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335085 | 351204 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EE | LL139EE | ll13 9ee | ll139ee | Wrexham | Wrecsam | Abenbury WwTW | 3203 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335256 | 351330 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EF | LL139EF | ll13 9ef | ll139ef | Wrexham | Wrecsam | Abenbury WwTW | 3298 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335030 | 351327 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EG | LL139EG | ll13 9eg | ll139eg | Wrexham | Wrecsam | Abenbury WwTW | 3530 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334880 | 351510 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EH | LL139EH | ll13 9eh | ll139eh | Wrexham | Wrecsam | Abenbury WwTW | 3359 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335021 | 351390 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EJ | LL139EJ | ll13 9ej | ll139ej | Wrexham | Wrecsam | Holt STW | 1044 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340962 | 353906 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EL | LL139EL | ll13 9el | ll139el | Wrexham | Wrecsam | Abenbury WwTW | 3594 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334886 | 351585 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EN | LL139EN | ll13 9en | ll139en | Wrexham | Wrecsam | Abenbury WwTW | 3274 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334974 | 351269 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EP | LL139EP | ll13 9ep | ll139ep | Wrexham | Wrecsam | Abenbury WwTW | 3607 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334964 | 351639 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EQ | LL139EQ | ll13 9eq | ll139eq | Wrexham | Wrecsam | Abenbury WwTW | 3090 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334838 | 350972 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9ER | LL139ER | ll13 9er | ll139er | Wrexham | Wrecsam | Abenbury WwTW | 3595 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334807 | 351543 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9ES | LL139ES | ll13 9es | ll139es | Wrexham | Wrecsam | Abenbury WwTW | 3455 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334869 | 351418 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9ET | LL139ET | ll13 9et | ll139et | Wrexham | Wrecsam | Abenbury WwTW | 3361 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334847 | 351297 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EU | LL139EU | ll13 9eu | ll139eu | Wrexham | Wrecsam | Abenbury WwTW | 2866 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334740 | 350621 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EW | LL139EW | ll13 9ew | ll139ew | Wrexham | Wrecsam | Abenbury WwTW | 3511 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 334965 | 351532 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EX | LL139EX | ll13 9ex | ll139ex | Wrexham | Wrecsam | Abenbury WwTW | 3257 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335155 | 351343 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EY | LL139EY | ll13 9ey | ll139ey | Wrexham | Wrecsam | Abenbury WwTW | 3025 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334694 | 350787 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9EZ | LL139EZ | ll13 9ez | ll139ez | Wrexham | Wrecsam | Abenbury WwTW | 3196 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335057 | 351226 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9FS | LL139FS | ll13 9fs | ll139fs | Wrexham | Wrecsam | Abenbury WwTW | 1872 | 707 | 700to900 | 1.41 | 1.03 | 0.76 | 13.16 | 7.02 | 7.76 | 337311 | 350114 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9FW | LL139FW | ll13 9fw | ll139fw | Wrexham | Wrecsam | Holt STW | 1374 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340669 | 353456 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9FX | LL139FX | ll13 9fx | ll139fx | Wrexham | Wrecsam | Abenbury WwTW | 2994 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335687 | 351268 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9FY | LL139FY | ll13 9fy | ll139fy | Wrexham | Wrecsam | Abenbury WwTW | 2979 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335751 | 351271 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9FZ | LL139FZ | ll13 9fz | ll139fz | Wrexham | Wrecsam | Abenbury WwTW | 1181 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 337526 | 349073 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GA | LL139GA | ll13 9ga | ll139ga | Wrexham | Wrecsam | Abenbury WwTW | 3025 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335302 | 351156 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GB | LL139GB | ll13 9gb | ll139gb | Wrexham | Wrecsam | Abenbury WwTW | 2990 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335234 | 351085 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GD | LL139GD | ll13 9gd | ll139gd | Wrexham | Wrecsam | Abenbury WwTW | 3209 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335354 | 351378 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GE | LL139GE | ll13 9ge | ll139ge | Wrexham | Wrecsam | Abenbury WwTW | 3228 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335523 | 351461 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GF | LL139GF | ll13 9gf | ll139gf | Wrexham | Wrecsam | Abenbury WwTW | 3114 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335802 | 351424 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GG | LL139GG | ll13 9gg | ll139gg | Wrexham | Wrecsam | Abenbury WwTW | 3018 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335811 | 351327 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GJ | LL139GJ | ll13 9gj | ll139gj | Wrexham | Wrecsam | Abenbury WwTW | 3165 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335679 | 351444 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GL | LL139GL | ll13 9gl | ll139gl | Wrexham | Wrecsam | Abenbury WwTW | 3134 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335553 | 351372 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GN | LL139GN | ll13 9gn | ll139gn | Wrexham | Wrecsam | Abenbury WwTW | 3158 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335817 | 351473 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GP | LL139GP | ll13 9gp | ll139gp | Wrexham | Wrecsam | Abenbury WwTW | 3031 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335538 | 351257 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GQ | LL139GQ | ll13 9gq | ll139gq | Wrexham | Wrecsam | Abenbury WwTW | 3084 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335498 | 351299 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GR | LL139GR | ll13 9gr | ll139gr | Wrexham | Wrecsam | Abenbury WwTW | 3079 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335452 | 351277 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GS | LL139GS | ll13 9gs | ll139gs | Wrexham | Wrecsam | Abenbury WwTW | 3219 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335439 | 351422 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GT | LL139GT | ll13 9gt | ll139gt | Wrexham | Wrecsam | Abenbury WwTW | 3276 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335718 | 351569 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GU | LL139GU | ll13 9gu | ll139gu | Wrexham | Wrecsam | Abenbury WwTW | 3311 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335663 | 351591 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GW | LL139GW | ll13 9gw | ll139gw | Wrexham | Wrecsam | Abenbury WwTW | 3275 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335614 | 351539 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GX | LL139GX | ll13 9gx | ll139gx | Wrexham | Wrecsam | Abenbury WwTW | 3139 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335388 | 351316 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GY | LL139GY | ll13 9gy | ll139gy | Wrexham | Wrecsam | Abenbury WwTW | 3151 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335500 | 351371 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9GZ | LL139GZ | ll13 9gz | ll139gz | Wrexham | Wrecsam | Abenbury WwTW | 3126 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335737 | 351419 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HA | LL139HA | ll13 9ha | ll139ha | Wrexham | Wrecsam | Abenbury WwTW | 2850 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334798 | 350647 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HB | LL139HB | ll13 9hb | ll139hb | Wrexham | Wrecsam | Abenbury WwTW | 2760 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334707 | 350453 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HD | LL139HD | ll13 9hd | ll139hd | Wrexham | Wrecsam | Abenbury WwTW | 2649 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334899 | 350470 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HE | LL139HE | ll13 9he | ll139he | Wrexham | Wrecsam | Abenbury WwTW | 2656 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334959 | 350525 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HF | LL139HF | ll13 9hf | ll139hf | Wrexham | Wrecsam | Abenbury WwTW | 2585 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 334980 | 350452 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HG | LL139HG | ll13 9hg | ll139hg | Wrexham | Wrecsam | Abenbury WwTW | 2496 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335026 | 350376 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HH | LL139HH | ll13 9hh | ll139hh | Wrexham | Wrecsam | Abenbury WwTW | 2545 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335101 | 350491 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HJ | LL139HJ | ll13 9hj | ll139hj | Wrexham | Wrecsam | Holt STW | 937 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340797 | 353944 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HL | LL139HL | ll13 9hl | ll139hl | Wrexham | Wrecsam | Abenbury WwTW | 2506 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335262 | 350549 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HN | LL139HN | ll13 9hn | ll139hn | Wrexham | Wrecsam | Abenbury WwTW | 2494 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335141 | 350457 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HP | LL139HP | ll13 9hp | ll139hp | Wrexham | Wrecsam | Abenbury WwTW | 2456 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335120 | 350396 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HQ | LL139HQ | ll13 9hq | ll139hq | Wrexham | Wrecsam | Abenbury WwTW | 3415 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335376 | 351607 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HR | LL139HR | ll13 9hr | ll139hr | Wrexham | Wrecsam | Abenbury WwTW | 2379 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335256 | 350396 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HS | LL139HS | ll13 9hs | ll139hs | Wrexham | Wrecsam | Abenbury WwTW | 2403 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335302 | 350453 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HT | LL139HT | ll13 9ht | ll139ht | Wrexham | Wrecsam | Abenbury WwTW | 2336 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335202 | 350307 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HU | LL139HU | ll13 9hu | ll139hu | Wrexham | Wrecsam | Abenbury WwTW | 2275 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335347 | 350330 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HW | LL139HW | ll13 9hw | ll139hw | Wrexham | Wrecsam | Abenbury WwTW | 2468 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335295 | 350525 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HX | LL139HX | ll13 9hx | ll139hx | Wrexham | Wrecsam | Abenbury WwTW | 1847 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335182 | 349638 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HY | LL139HY | ll13 9hy | ll139hy | Wrexham | Wrecsam | Abenbury WwTW | 2249 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335345 | 350298 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9HZ | LL139HZ | ll13 9hz | ll139hz | Wrexham | Wrecsam | Abenbury WwTW | 3504 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335335 | 351687 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JA | LL139JA | ll13 9ja | ll139ja | Wrexham | Wrecsam | Holt STW | 970 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340814 | 353915 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JB | LL139JB | ll13 9jb | ll139jb | Wrexham | Wrecsam | Holt STW | 2181 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 338494 | 353827 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JD | LL139JD | ll13 9jd | ll139jd | Wrexham | Wrecsam | Holt STW | 1035 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341013 | 353949 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JE | LL139JE | ll13 9je | ll139je | Wrexham | Wrecsam | Holt STW | 778 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340973 | 354243 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JF | LL139JF | ll13 9jf | ll139jf | Wrexham | Wrecsam | Holt STW | 836 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341014 | 354202 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JG | LL139JG | ll13 9jg | ll139jg | Wrexham | Wrecsam | Holt STW | 923 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341142 | 354211 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JH | LL139JH | ll13 9jh | ll139jh | Wrexham | Wrecsam | Holt STW | 858 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341116 | 354282 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JJ | LL139JJ | ll13 9jj | ll139jj | Wrexham | Wrecsam | Holt STW | 873 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341114 | 354256 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JL | LL139JL | ll13 9jl | ll139jl | Wrexham | Wrecsam | Holt STW | 896 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341110 | 354215 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JN | LL139JN | ll13 9jn | ll139jn | Wrexham | Wrecsam | Holt STW | 903 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341067 | 354160 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JP | LL139JP | ll13 9jp | ll139jp | Wrexham | Wrecsam | Holt STW | 1053 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341145 | 354028 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JQ | LL139JQ | ll13 9jq | ll139jq | Wrexham | Wrecsam | Holt STW | 937 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341146 | 354194 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JR | LL139JR | ll13 9jr | ll139jr | Wrexham | Wrecsam | Holt STW | 1020 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341097 | 354030 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JS | LL139JS | ll13 9js | ll139js | Wrexham | Wrecsam | Holt STW | 866 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340964 | 354121 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JT | LL139JT | ll13 9jt | ll139jt | Wrexham | Wrecsam | Isycoed Marshlea STW | 2073 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 337794 | 350384 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JW | LL139JW | ll13 9jw | ll139jw | Wrexham | Wrecsam | Holt STW | 967 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341078 | 354084 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JX | LL139JX | ll13 9jx | ll139jx | Wrexham | Wrecsam | Holt STW | 1037 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341087 | 354000 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JY | LL139JY | ll13 9jy | ll139jy | Wrexham | Wrecsam | Abenbury WwTW | 3692 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335629 | 351976 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9JZ | LL139JZ | ll13 9jz | ll139jz | Wrexham | Wrecsam | Holt STW | 1008 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340992 | 353967 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LA | LL139LA | ll13 9la | ll139la | Wrexham | Wrecsam | Abenbury WwTW | 2223 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335328 | 350257 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LB | LL139LB | ll13 9lb | ll139lb | Wrexham | Wrecsam | Abenbury WwTW | 2144 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335373 | 350192 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LD | LL139LD | ll13 9ld | ll139ld | Wrexham | Wrecsam | Abenbury WwTW | 2076 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335355 | 350097 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LE | LL139LE | ll13 9le | ll139le | Wrexham | Wrecsam | Abenbury WwTW | 2121 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335308 | 350119 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LF | LL139LF | ll13 9lf | ll139lf | Wrexham | Wrecsam | Abenbury WwTW | 2082 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335276 | 350046 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LG | LL139LG | ll13 9lg | ll139lg | Wrexham | Wrecsam | Abenbury WwTW | 2169 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335200 | 350097 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LH | LL139LH | ll13 9lh | ll139lh | Wrexham | Wrecsam | Abenbury WwTW | 2151 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335252 | 350114 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LJ | LL139LJ | ll13 9lj | ll139lj | Wrexham | Wrecsam | Gresford STW | 3694 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335339 | 352116 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LL | LL139LL | ll13 9ll | ll139ll | Wrexham | Wrecsam | Abenbury WwTW | 2189 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335223 | 350140 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LN | LL139LN | ll13 9ln | ll139ln | Wrexham | Wrecsam | Abenbury WwTW | 2228 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335166 | 350145 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LP | LL139LP | ll13 9lp | ll139lp | Wrexham | Wrecsam | Abenbury WwTW | 2377 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335034 | 350230 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LQ | LL139LQ | ll13 9lq | ll139lq | Wrexham | Wrecsam | Abenbury WwTW | 2339 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335068 | 350208 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LR | LL139LR | ll13 9lr | ll139lr | Wrexham | Wrecsam | Abenbury WwTW | 2276 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335169 | 350208 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LS | LL139LS | ll13 9ls | ll139ls | Wrexham | Wrecsam | Abenbury WwTW | 2452 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335081 | 350362 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LT | LL139LT | ll13 9lt | ll139lt | Wrexham | Wrecsam | Abenbury WwTW | 2413 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335077 | 350310 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LU | LL139LU | ll13 9lu | ll139lu | Wrexham | Wrecsam | Abenbury WwTW | 2453 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335002 | 350301 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LW | LL139LW | ll13 9lw | ll139lw | Wrexham | Wrecsam | Abenbury WwTW | 2311 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335085 | 350186 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LX | LL139LX | ll13 9lx | ll139lx | Wrexham | Wrecsam | Gresford STW | 3749 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335414 | 352071 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LY | LL139LY | ll13 9ly | ll139ly | Wrexham | Wrecsam | Abenbury WwTW | 2423 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335136 | 350367 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9LZ | LL139LZ | ll13 9lz | ll139lz | Wrexham | Wrecsam | Gresford STW | 3673 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335388 | 352144 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NA | LL139NA | ll13 9na | ll139na | Wrexham | Wrecsam | Abenbury WwTW | 2437 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335205 | 350432 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NB | LL139NB | ll13 9nb | ll139nb | Wrexham | Wrecsam | Abenbury WwTW | 3108 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335261 | 351228 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9ND | LL139ND | ll13 9nd | ll139nd | Wrexham | Wrecsam | Abenbury WwTW | 3142 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335265 | 351267 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NE | LL139NE | ll13 9ne | ll139ne | Wrexham | Wrecsam | Abenbury WwTW | 3077 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335240 | 351184 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NF | LL139NF | ll13 9nf | ll139nf | Wrexham | Wrecsam | Abenbury WwTW | 3111 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335188 | 351197 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NG | LL139NG | ll13 9ng | ll139ng | Wrexham | Wrecsam | Abenbury WwTW | 2843 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335100 | 350845 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NH | LL139NH | ll13 9nh | ll139nh | Wrexham | Wrecsam | Abenbury WwTW | 2979 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335196 | 351053 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NJ | LL139NJ | ll13 9nj | ll139nj | Wrexham | Wrecsam | Abenbury WwTW | 3702 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335383 | 351914 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NN | LL139NN | ll13 9nn | ll139nn | Wrexham | Wrecsam | Abenbury WwTW | 2525 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335315 | 350602 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NP | LL139NP | ll13 9np | ll139np | Wrexham | Wrecsam | Abenbury WwTW | 2316 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335378 | 350397 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NQ | LL139NQ | ll13 9nq | ll139nq | Wrexham | Wrecsam | Abenbury WwTW | 3759 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335392 | 351977 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NR | LL139NR | ll13 9nr | ll139nr | Wrexham | Wrecsam | Abenbury WwTW | 2081 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335411 | 350141 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NS | LL139NS | ll13 9ns | ll139ns | Wrexham | Wrecsam | Abenbury WwTW | 2010 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335366 | 350023 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NT | LL139NT | ll13 9nt | ll139nt | Wrexham | Wrecsam | Abenbury WwTW | 1969 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335345 | 349956 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NU | LL139NU | ll13 9nu | ll139nu | Wrexham | Wrecsam | Abenbury WwTW | 1913 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335327 | 349870 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NW | LL139NW | ll13 9nw | ll139nw | Wrexham | Wrecsam | Abenbury WwTW | 2424 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 335349 | 350505 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NX | LL139NX | ll13 9nx | ll139nx | Wrexham | Wrecsam | Abenbury WwTW | 2170 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335068 | 349983 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NY | LL139NY | ll13 9ny | ll139ny | Wrexham | Wrecsam | Abenbury WwTW | 1823 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335340 | 349762 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9NZ | LL139NZ | ll13 9nz | ll139nz | Wrexham | Wrecsam | Abenbury WwTW | 3771 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335296 | 351957 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PA | LL139PA | ll13 9pa | ll139pa | Wrexham | Wrecsam | Abenbury WwTW | 1677 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335367 | 349587 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PB | LL139PB | ll13 9pb | ll139pb | Wrexham | Wrecsam | Abenbury WwTW | 1759 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335291 | 349627 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PD | LL139PD | ll13 9pd | ll139pd | Wrexham | Wrecsam | Abenbury WwTW | 1817 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335227 | 349643 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PE | LL139PE | ll13 9pe | ll139pe | Wrexham | Wrecsam | Abenbury WwTW | 1955 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335191 | 349803 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PF | LL139PF | ll13 9pf | ll139pf | Wrexham | Wrecsam | Abenbury WwTW | 2085 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335111 | 349907 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PG | LL139PG | ll13 9pg | ll139pg | Wrexham | Wrecsam | Abenbury WwTW | 2202 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335017 | 349979 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PH | LL139PH | ll13 9ph | ll139ph | Wrexham | Wrecsam | Isycoed Marshlea STW | 1443 | 688 | 600to700 | 1.37 | 1.01 | 0.74 | 12.8 | 6.83 | 7.54 | 339104 | 349568 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PJ | LL139PJ | ll13 9pj | ll139pj | Wrexham | Wrecsam | Abenbury WwTW | 3109 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335697 | 351390 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PL | LL139PL | ll13 9pl | ll139pl | Wrexham | Wrecsam | Abenbury WwTW | 1991 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335213 | 349874 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PN | LL139PN | ll13 9pn | ll139pn | Wrexham | Wrecsam | Isycoed Marshlea STW | 1695 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 338460 | 349810 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PQ | LL139PQ | ll13 9pq | ll139pq | Wrexham | Wrecsam | Bowling Bank STW | 1370 | 680 | 600to700 | 1.36 | 0.99 | 0.73 | 12.64 | 6.74 | 7.45 | 339313 | 349377 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PR | LL139PR | ll13 9pr | ll139pr | Wrexham | Wrecsam | Abenbury WwTW | 709 | 704 | 700to900 | 1.41 | 1.03 | 0.75 | 13.11 | 6.99 | 7.73 | 337260 | 348463 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PS | LL139PS | ll13 9ps | ll139ps | Wrexham | Wrecsam | Abenbury WwTW | 1368 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 337601 | 349283 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PT | LL139PT | ll13 9pt | ll139pt | Wrexham | Wrecsam | Abenbury WwTW | 874 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 337291 | 348873 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PU | LL139PU | ll13 9pu | ll139pu | Wrexham | Wrecsam | Abenbury WwTW | 1081 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 337415 | 349056 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PW | LL139PW | ll13 9pw | ll139pw | Wrexham | Wrecsam | Isycoed Marshlea STW | 1685 | 688 | 600to700 | 1.37 | 1.01 | 0.74 | 12.8 | 6.83 | 7.54 | 338685 | 349575 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PY | LL139PY | ll13 9py | ll139py | Wrexham | Wrecsam | Abenbury WwTW | 962 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 337216 | 349101 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9PZ | LL139PZ | ll13 9pz | ll139pz | Wrexham | Wrecsam | Abenbury WwTW | 3535 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335778 | 351851 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QA | LL139QA | ll13 9qa | ll139qa | Wrexham | Wrecsam | Abenbury WwTW | 1765 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 338067 | 349310 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QB | LL139QB | ll13 9qb | ll139qb | Wrexham | Wrecsam | Abenbury WwTW | 3333 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335407 | 351531 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QD | LL139QD | ll13 9qd | ll139qd | Wrexham | Wrecsam | Abenbury WwTW | 3372 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335510 | 351608 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QE | LL139QE | ll13 9qe | ll139qe | Wrexham | Wrecsam | Abenbury WwTW | 1529 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 337936 | 349056 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QF | LL139QF | ll13 9qf | ll139qf | Wrexham | Wrecsam | Bowling Bank STW | 1141 | 668 | 600to700 | 1.33 | 0.97 | 0.71 | 12.41 | 6.62 | 7.32 | 340723 | 348930 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QG | LL139QG | ll13 9qg | ll139qg | Wrexham | Wrecsam | Abenbury WwTW | 3360 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335461 | 351579 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QH | LL139QH | ll13 9qh | ll139qh | Wrexham | Wrecsam | Abenbury WwTW | 3563 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335422 | 351780 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QJ | LL139QJ | ll13 9qj | ll139qj | Wrexham | Wrecsam | Abenbury WwTW | 3592 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335273 | 351758 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QL | LL139QL | ll13 9ql | ll139ql | Wrexham | Wrecsam | Gresford STW | 3699 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335447 | 352126 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QN | LL139QN | ll13 9qn | ll139qn | Wrexham | Wrecsam | Gresford STW | 3759 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335535 | 352080 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QP | LL139QP | ll13 9qp | ll139qp | Wrexham | Wrecsam | Abenbury WwTW | 3438 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335451 | 351658 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QQ | LL139QQ | ll13 9qq | ll139qq | Wrexham | Wrecsam | Abenbury WwTW | 3778 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335582 | 352052 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QR | LL139QR | ll13 9qr | ll139qr | Wrexham | Wrecsam | Abenbury WwTW | 3493 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335547 | 351746 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QS | LL139QS | ll13 9qs | ll139qs | Wrexham | Wrecsam | Abenbury WwTW | 1594 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 337790 | 349408 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QT | LL139QT | ll13 9qt | ll139qt | Wrexham | Wrecsam | Abenbury WwTW | 3395 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335680 | 351682 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QU | LL139QU | ll13 9qu | ll139qu | Wrexham | Wrecsam | Abenbury WwTW | 3595 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335488 | 351835 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QW | LL139QW | ll13 9qw | ll139qw | Wrexham | Wrecsam | Abenbury WwTW | 3683 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335579 | 351953 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QX | LL139QX | ll13 9qx | ll139qx | Wrexham | Wrecsam | Abenbury WwTW | 3445 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335585 | 351708 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QY | LL139QY | ll13 9qy | ll139qy | Wrexham | Wrecsam | Abenbury WwTW | 3476 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335636 | 351754 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9QZ | LL139QZ | ll13 9qz | ll139qz | Wrexham | Wrecsam | Abenbury WwTW | 3732 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335521 | 351988 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RA | LL139RA | ll13 9ra | ll139ra | Wrexham | Wrecsam | Abenbury WwTW | 849 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 337233 | 348913 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RB | LL139RB | ll13 9rb | ll139rb | Wrexham | Wrecsam | Abenbury WwTW | 1048 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 337426 | 348983 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RD | LL139RD | ll13 9rd | ll139rd | Wrexham | Wrecsam | Isycoed Marshlea STW | 2014 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 338288 | 349513 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RE | LL139RE | ll13 9re | ll139re | Wrexham | Wrecsam | Isycoed Marshlea STW | 1872 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 338426 | 349571 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RF | LL139RF | ll13 9rf | ll139rf | Wrexham | Wrecsam | Isycoed Marshlea STW | 1670 | 698 | 600to700 | 1.39 | 1.02 | 0.75 | 12.99 | 6.93 | 7.66 | 338176 | 350527 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RG | LL139RG | ll13 9rg | ll139rg | Wrexham | Wrecsam | Bowling Bank STW | 1327 | 680 | 600to700 | 1.36 | 0.99 | 0.73 | 12.64 | 6.74 | 7.45 | 339124 | 349216 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RH | LL139RH | ll13 9rh | ll139rh | Wrexham | Wrecsam | Bowling Bank STW | 384 | 671 | 600to700 | 1.34 | 0.98 | 0.72 | 12.47 | 6.65 | 7.35 | 339810 | 348513 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RJ | LL139RJ | ll13 9rj | ll139rj | Wrexham | Wrecsam | Isycoed Marshlea STW | 1779 | 688 | 600to700 | 1.37 | 1.01 | 0.74 | 12.8 | 6.83 | 7.54 | 338500 | 349629 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RL | LL139RL | ll13 9rl | ll139rl | Wrexham | Wrecsam | Bowling Bank STW | 1318 | 671 | 600to700 | 1.34 | 0.98 | 0.72 | 12.47 | 6.65 | 7.35 | 340046 | 349449 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RN | LL139RN | ll13 9rn | ll139rn | Wrexham | Wrecsam | Isycoed Marshlea STW | 436 | 680 | 600to700 | 1.36 | 0.99 | 0.73 | 12.64 | 6.74 | 7.45 | 339808 | 350384 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RP | LL139RP | ll13 9rp | ll139rp | Wrexham | Wrecsam | Bowling Bank STW | 890 | 668 | 600to700 | 1.33 | 0.97 | 0.71 | 12.41 | 6.62 | 7.32 | 340779 | 348279 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RQ | LL139RQ | ll13 9rq | ll139rq | Wrexham | Wrecsam | Abenbury WwTW | 3769 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335419 | 351996 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RR | LL139RR | ll13 9rr | ll139rr | Wrexham | Wrecsam | Bowling Bank STW | 979 | 668 | 600to700 | 1.33 | 0.97 | 0.71 | 12.41 | 6.62 | 7.32 | 340608 | 348816 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RS | LL139RS | ll13 9rs | ll139rs | Wrexham | Wrecsam | Bowling Bank STW | 1210 | 668 | 600to700 | 1.33 | 0.97 | 0.71 | 12.41 | 6.62 | 7.32 | 340761 | 348990 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RT | LL139RT | ll13 9rt | ll139rt | Wrexham | Wrecsam | Isycoed Marshlea STW | 1738 | 669 | 600to700 | 1.33 | 0.98 | 0.72 | 12.43 | 6.63 | 7.33 | 341028 | 349572 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RU | LL139RU | ll13 9ru | ll139ru | Wrexham | Wrecsam | Isycoed Marshlea STW | 931 | 674 | 600to700 | 1.34 | 0.98 | 0.72 | 12.53 | 6.68 | 7.39 | 340693 | 351143 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RW | LL139RW | ll13 9rw | ll139rw | Wrexham | Wrecsam | Bowling Bank STW | 285 | 671 | 600to700 | 1.34 | 0.98 | 0.72 | 12.47 | 6.65 | 7.35 | 340137 | 348299 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RX | LL139RX | ll13 9rx | ll139rx | Wrexham | Wrecsam | Isycoed Marshlea STW | 1469 | 698 | 600to700 | 1.39 | 1.02 | 0.75 | 12.99 | 6.93 | 7.66 | 338363 | 350634 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RY | LL139RY | ll13 9ry | ll139ry | Wrexham | Wrecsam | Isycoed Marshlea STW | 808 | 680 | 600to700 | 1.36 | 0.99 | 0.73 | 12.64 | 6.74 | 7.45 | 340389 | 350247 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9RZ | LL139RZ | ll13 9rz | ll139rz | Wrexham | Wrecsam | Abenbury WwTW | 3705 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335278 | 351880 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SA | LL139SA | ll13 9sa | ll139sa | Wrexham | Wrecsam | Abenbury WwTW | 3528 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 335932 | 351874 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SB | LL139SB | ll13 9sb | ll139sb | Wrexham | Wrecsam | Abenbury WwTW | 3591 | 735 | 700to900 | 1.47 | 1.08 | 0.79 | 13.7 | 7.31 | 8.07 | 336187 | 351974 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SD | LL139SD | ll13 9sd | ll139sd | Wrexham | Wrecsam | Isycoed Marshlea STW | 3087 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 336914 | 351857 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SE | LL139SE | ll13 9se | ll139se | Wrexham | Wrecsam | Gresford STW | 3622 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 336632 | 352611 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SF | LL139SF | ll13 9sf | ll139sf | Wrexham | Wrecsam | Isycoed Marshlea STW | 3301 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 336678 | 351829 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SG | LL139SG | ll13 9sg | ll139sg | Wrexham | Wrecsam | Isycoed Marshlea STW | 2987 | 716 | 700to900 | 1.43 | 1.05 | 0.77 | 13.34 | 7.11 | 7.86 | 337229 | 352305 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SH | LL139SH | ll13 9sh | ll139sh | Wrexham | Wrecsam | Isycoed Marshlea STW | 2312 | 706 | 700to900 | 1.41 | 1.03 | 0.76 | 13.15 | 7.01 | 7.75 | 337860 | 352045 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SJ | LL139SJ | ll13 9sj | ll139sj | Wrexham | Wrecsam | Abenbury WwTW | 2908 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 336268 | 351296 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SL | LL139SL | ll13 9sl | ll139sl | Wrexham | Wrecsam | Holt STW | 848 | 686 | 600to700 | 1.37 | 1 | 0.73 | 12.76 | 6.81 | 7.52 | 340204 | 353996 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SQ | LL139SQ | ll13 9sq | ll139sq | Wrexham | Wrecsam | Abenbury WwTW | 920 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 337383 | 348801 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SS | LL139SS | ll13 9ss | ll139ss | Wrexham | Wrecsam | Holt STW | 1996 | 692 | 600to700 | 1.38 | 1.01 | 0.74 | 12.88 | 6.87 | 7.59 | 339456 | 353074 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9ST | LL139ST | ll13 9st | ll139st | Wrexham | Wrecsam | Holt STW | 1643 | 686 | 600to700 | 1.37 | 1 | 0.73 | 12.76 | 6.81 | 7.52 | 339822 | 353288 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SU | LL139SU | ll13 9su | ll139su | Wrexham | Wrecsam | Holt STW | 875 | 686 | 600to700 | 1.37 | 1 | 0.73 | 12.76 | 6.81 | 7.52 | 340230 | 353961 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SW | LL139SW | ll13 9sw | ll139sw | Wrexham | Wrecsam | Isycoed Marshlea STW | 2085 | 692 | 600to700 | 1.38 | 1.01 | 0.74 | 12.88 | 6.87 | 7.59 | 338725 | 352594 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SX | LL139SX | ll13 9sx | ll139sx | Wrexham | Wrecsam | Abenbury WwTW | 3559 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335356 | 351753 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SY | LL139SY | ll13 9sy | ll139sy | Wrexham | Wrecsam | Holt STW | 1349 | 690 | 600to700 | 1.38 | 1.01 | 0.74 | 12.84 | 6.85 | 7.57 | 339155 | 354402 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9SZ | LL139SZ | ll13 9sz | ll139sz | Wrexham | Wrecsam | Gresford STW | 3269 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 334868 | 352512 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TA | LL139TA | ll13 9ta | ll139ta | Wrexham | Wrecsam | Holt STW | 2564 | 692 | 600to700 | 1.38 | 1.01 | 0.74 | 12.88 | 6.87 | 7.59 | 338512 | 353121 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TE | LL139TE | ll13 9te | ll139te | Wrexham | Wrecsam | Holt STW | 2240 | 700 | 700to900 | 1.4 | 1.02 | 0.75 | 13.03 | 6.95 | 7.68 | 338280 | 354219 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TF | LL139TF | ll13 9tf | ll139tf | Wrexham | Wrecsam | Holt STW | 2900 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 337882 | 353445 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TG | LL139TG | ll13 9tg | ll139tg | Wrexham | Wrecsam | Gresford STW | 2975 | 718 | 700to900 | 1.44 | 1.05 | 0.77 | 13.37 | 7.13 | 7.88 | 336960 | 353654 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TH | LL139TH | ll13 9th | ll139th | Wrexham | Wrecsam | Gresford STW | 2748 | 718 | 700to900 | 1.44 | 1.05 | 0.77 | 13.37 | 7.13 | 7.88 | 336662 | 353689 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TJ | LL139TJ | ll13 9tj | ll139tj | Wrexham | Wrecsam | Gresford STW | 3018 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 334597 | 352776 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TL | LL139TL | ll13 9tl | ll139tl | Wrexham | Wrecsam | Gresford STW | 2906 | 717 | 700to900 | 1.43 | 1.05 | 0.77 | 13.36 | 7.12 | 7.87 | 336566 | 353414 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TN | LL139TN | ll13 9tn | ll139tn | Wrexham | Wrecsam | Gresford STW | 2947 | 738 | 700to900 | 1.48 | 1.08 | 0.79 | 13.75 | 7.34 | 8.11 | 335930 | 353028 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TP | LL139TP | ll13 9tp | ll139tp | Wrexham | Wrecsam | Gresford STW | 3029 | 738 | 700to900 | 1.48 | 1.08 | 0.79 | 13.75 | 7.34 | 8.11 | 335521 | 352821 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TQ | LL139TQ | ll13 9tq | ll139tq | Wrexham | Wrecsam | Gresford STW | 3080 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 334704 | 352706 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TR | LL139TR | ll13 9tr | ll139tr | Wrexham | Wrecsam | Gresford STW | 3473 | 755 | 700to900 | 1.51 | 1.11 | 0.81 | 14.07 | 7.51 | 8.3 | 335359 | 352341 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TS | LL139TS | ll13 9ts | ll139ts | Wrexham | Wrecsam | Holt STW | 1350 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340720 | 353490 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TT | LL139TT | ll13 9tt | ll139tt | Wrexham | Wrecsam | Abenbury WwTW | 2090 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335462 | 350184 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TU | LL139TU | ll13 9tu | ll139tu | Wrexham | Wrecsam | Abenbury WwTW | 1646 | 746 | 700to900 | 1.49 | 1.09 | 0.8 | 13.9 | 7.42 | 8.2 | 335440 | 349614 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TW | LL139TW | ll13 9tw | ll139tw | Wrexham | Wrecsam | Gresford STW | 3125 | 738 | 700to900 | 1.48 | 1.08 | 0.79 | 13.75 | 7.34 | 8.11 | 335721 | 352771 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TX | LL139TX | ll13 9tx | ll139tx | Wrexham | Wrecsam | Gresford STW | 3064 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334494 | 352741 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TY | LL139TY | ll13 9ty | ll139ty | Wrexham | Wrecsam | Abenbury WwTW | 2843 | 731 | 700to900 | 1.46 | 1.07 | 0.78 | 13.62 | 7.26 | 8.03 | 335834 | 351152 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9TZ | LL139TZ | ll13 9tz | ll139tz | Wrexham | Wrecsam | Gresford STW | 2991 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334370 | 352834 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UA | LL139UA | ll13 9ua | ll139ua | Wrexham | Wrecsam | Isycoed Marshlea STW | 1576 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 338324 | 350326 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UB | LL139UB | ll13 9ub | ll139ub | Wrexham | Wrecsam | Isycoed Marshlea STW | 2636 | 710 | 700to900 | 1.42 | 1.04 | 0.76 | 13.22 | 7.05 | 7.79 | 337232 | 351315 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UD | LL139UD | ll13 9ud | ll139ud | Wrexham | Wrecsam | Abenbury WwTW | 2353 | 710 | 700to900 | 1.42 | 1.04 | 0.76 | 13.22 | 7.05 | 7.79 | 337288 | 350638 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UE | LL139UE | ll13 9ue | ll139ue | Wrexham | Wrecsam | Isycoed Marshlea STW | 1348 | 688 | 600to700 | 1.37 | 1.01 | 0.74 | 12.8 | 6.83 | 7.54 | 338560 | 350343 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UF | LL139UF | ll13 9uf | ll139uf | Wrexham | Wrecsam | Isycoed Marshlea STW | 1916 | 698 | 600to700 | 1.39 | 1.02 | 0.75 | 12.99 | 6.93 | 7.66 | 337926 | 350537 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UG | LL139UG | ll13 9ug | ll139ug | Wrexham | Wrecsam | Isycoed Marshlea STW | 1861 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 338068 | 350193 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UH | LL139UH | ll13 9uh | ll139uh | Wrexham | Wrecsam | Abenbury WwTW | 1620 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 337623 | 349620 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UJ | LL139UJ | ll13 9uj | ll139uj | Wrexham | Wrecsam | Gresford STW | 2921 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334371 | 352905 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UL | LL139UL | ll13 9ul | ll139ul | Wrexham | Wrecsam | Isycoed Marshlea STW | 1685 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 338278 | 350141 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UN | LL139UN | ll13 9un | ll139un | Wrexham | Wrecsam | Gresford STW | 3076 | 758 | 700to900 | 1.52 | 1.11 | 0.81 | 14.13 | 7.54 | 8.33 | 334573 | 352720 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UQ | LL139UQ | ll13 9uq | ll139uq | Wrexham | Wrecsam | Gresford STW | 2967 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334472 | 352842 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UR | LL139UR | ll13 9ur | ll139ur | Wrexham | Wrecsam | Isycoed Marshlea STW | 491 | 694 | 600to700 | 1.39 | 1.01 | 0.74 | 12.92 | 6.89 | 7.61 | 339427 | 351114 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9US | LL139US | ll13 9us | ll139us | Wrexham | Wrecsam | Isycoed Marshlea STW | 501 | 683 | 600to700 | 1.36 | 1 | 0.73 | 12.7 | 6.77 | 7.49 | 339801 | 351320 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UT | LL139UT | ll13 9ut | ll139ut | Wrexham | Wrecsam | Isycoed Marshlea STW | 1056 | 688 | 600to700 | 1.37 | 1.01 | 0.74 | 12.8 | 6.83 | 7.54 | 338816 | 350494 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UU | LL139UU | ll13 9uu | ll139uu | Wrexham | Wrecsam | Isycoed Marshlea STW | 1637 | 688 | 600to700 | 1.37 | 1.01 | 0.74 | 12.8 | 6.83 | 7.54 | 338805 | 349537 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UW | LL139UW | ll13 9uw | ll139uw | Wrexham | Wrecsam | Isycoed Marshlea STW | 949 | 684 | 600to700 | 1.37 | 1 | 0.73 | 12.72 | 6.79 | 7.5 | 340448 | 351531 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UX | LL139UX | ll13 9ux | ll139ux | Wrexham | Wrecsam | Gresford STW | 3055 | 783 | 700to900 | 1.57 | 1.15 | 0.84 | 14.59 | 7.78 | 8.6 | 334334 | 352775 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UY | LL139UY | ll13 9uy | ll139uy | Wrexham | Wrecsam | Isycoed Marshlea STW | 1503 | 688 | 600to700 | 1.37 | 1.01 | 0.74 | 12.8 | 6.83 | 7.54 | 338826 | 349694 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9UZ | LL139UZ | ll13 9uz | ll139uz | Wrexham | Wrecsam | Abenbury WwTW | 2031 | 707 | 700to900 | 1.41 | 1.03 | 0.76 | 13.16 | 7.02 | 7.76 | 337333 | 350278 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9WB | LL139WB | ll13 9wb | ll139wb | Wrexham | Wrecsam | Isycoed Marshlea STW | 1349 | 688 | 600to700 | 1.37 | 1.01 | 0.74 | 12.8 | 6.83 | 7.54 | 338654 | 350142 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9WJ | LL139WJ | ll13 9wj | ll139wj | Wrexham | Wrecsam | Holt STW | 1468 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340804 | 353388 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XA | LL139XA | ll13 9xa | ll139xa | Wrexham | Wrecsam | Abenbury WwTW | 3294 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334566 | 351028 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XB | LL139XB | ll13 9xb | ll139xb | Wrexham | Wrecsam | Abenbury WwTW | 3263 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334537 | 350967 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XD | LL139XD | ll13 9xd | ll139xd | Wrexham | Wrecsam | Abenbury WwTW | 3234 | 750 | 700to900 | 1.5 | 1.1 | 0.81 | 13.98 | 7.46 | 8.24 | 334662 | 351025 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XE | LL139XE | ll13 9xe | ll139xe | Wrexham | Wrecsam | Abenbury WwTW | 1273 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 337305 | 349430 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XG | LL139XG | ll13 9xg | ll139xg | Wrexham | Wrecsam | Isycoed Marshlea STW | 1433 | 698 | 600to700 | 1.39 | 1.02 | 0.75 | 12.99 | 6.93 | 7.66 | 338410 | 350566 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XH | LL139XH | ll13 9xh | ll139xh | Wrexham | Wrecsam | Holt STW | 932 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340844 | 353970 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XJ | LL139XJ | ll13 9xj | ll139xj | Wrexham | Wrecsam | Holt STW | 911 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340852 | 353998 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XL | LL139XL | ll13 9xl | ll139xl | Wrexham | Wrecsam | Holt STW | 956 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340898 | 353971 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XN | LL139XN | ll13 9xn | ll139xn | Wrexham | Wrecsam | Abenbury WwTW | 1401 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 337438 | 349489 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XP | LL139XP | ll13 9xp | ll139xp | Wrexham | Wrecsam | Isycoed Marshlea STW | 1542 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 338400 | 350221 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XQ | LL139XQ | ll13 9xq | ll139xq | Wrexham | Wrecsam | Isycoed Marshlea STW | 1628 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 338411 | 350006 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XR | LL139XR | ll13 9xr | ll139xr | Wrexham | Wrecsam | Isycoed Marshlea STW | 1459 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 338442 | 350342 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XS | LL139XS | ll13 9xs | ll139xs | Wrexham | Wrecsam | Abenbury WwTW | 914 | 705 | 700to900 | 1.41 | 1.03 | 0.76 | 13.13 | 7 | 7.74 | 336989 | 349206 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XT | LL139XT | ll13 9xt | ll139xt | Wrexham | Wrecsam | Isycoed Marshlea STW | 1525 | 693 | 600to700 | 1.38 | 1.01 | 0.74 | 12.9 | 6.88 | 7.6 | 338453 | 350145 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XW | LL139XW | ll13 9xw | ll139xw | Wrexham | Wrecsam | Isycoed Marshlea STW | 926 | 694 | 600to700 | 1.39 | 1.01 | 0.74 | 12.92 | 6.89 | 7.61 | 338896 | 350763 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9XY | LL139XY | ll13 9xy | ll139xy | Wrexham | Wrecsam | Holt STW | 1174 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341069 | 353819 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YA | LL139YA | ll13 9ya | ll139ya | Wrexham | Wrecsam | Isycoed Marshlea STW | 1004 | 684 | 600to700 | 1.37 | 1 | 0.73 | 12.72 | 6.79 | 7.5 | 339973 | 351812 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YB | LL139YB | ll13 9yb | ll139yb | Wrexham | Wrecsam | Isycoed Marshlea STW | 1606 | 684 | 600to700 | 1.37 | 1 | 0.73 | 12.72 | 6.79 | 7.5 | 339665 | 352418 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YD | LL139YD | ll13 9yd | ll139yd | Wrexham | Wrecsam | Isycoed Marshlea STW | 2027 | 698 | 600to700 | 1.39 | 1.02 | 0.75 | 12.99 | 6.93 | 7.66 | 337878 | 351400 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YE | LL139YE | ll13 9ye | ll139ye | Wrexham | Wrecsam | Isycoed Marshlea STW | 2298 | 706 | 700to900 | 1.41 | 1.03 | 0.76 | 13.15 | 7.01 | 7.75 | 337703 | 351711 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YF | LL139YF | ll13 9yf | ll139yf | Wrexham | Wrecsam | Holt STW | 1204 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341201 | 353878 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YG | LL139YG | ll13 9yg | ll139yg | Wrexham | Wrecsam | Holt STW | 1071 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341046 | 353928 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YH | LL139YH | ll13 9yh | ll139yh | Wrexham | Wrecsam | Holt STW | 1188 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340987 | 353756 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YJ | LL139YJ | ll13 9yj | ll139yj | Wrexham | Wrecsam | Holt STW | 1344 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340800 | 353516 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YL | LL139YL | ll13 9yl | ll139yl | Wrexham | Wrecsam | Holt STW | 1139 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341020 | 353830 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YN | LL139YN | ll13 9yn | ll139yn | Wrexham | Wrecsam | Holt STW | 1124 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340974 | 353821 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YP | LL139YP | ll13 9yp | ll139yp | Wrexham | Wrecsam | Holt STW | 1335 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340898 | 353557 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YQ | LL139YQ | ll13 9yq | ll139yq | Wrexham | Wrecsam | Holt STW | 1315 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340922 | 353587 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YR | LL139YR | ll13 9yr | ll139yr | Wrexham | Wrecsam | Holt STW | 1388 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340841 | 353482 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YS | LL139YS | ll13 9ys | ll139ys | Wrexham | Wrecsam | Holt STW | 1345 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341013 | 353594 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YT | LL139YT | ll13 9yt | ll139yt | Wrexham | Wrecsam | Holt STW | 1364 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340907 | 353529 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YU | LL139YU | ll13 9yu | ll139yu | Wrexham | Wrecsam | Holt STW | 1274 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340717 | 353567 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YW | LL139YW | ll13 9yw | ll139yw | Wrexham | Wrecsam | Holt STW | 1168 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340934 | 353752 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YX | LL139YX | ll13 9yx | ll139yx | Wrexham | Wrecsam | Holt STW | 1165 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 341124 | 353868 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YY | LL139YY | ll13 9yy | ll139yy | Wrexham | Wrecsam | Holt STW | 1238 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340860 | 353646 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL13 9YZ | LL139YZ | ll13 9yz | ll139yz | Wrexham | Wrecsam | Holt STW | 1449 | 681 | 600to700 | 1.36 | 0.99 | 0.73 | 12.66 | 6.75 | 7.47 | 340842 | 353418 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AA | LL141AA | ll14 1aa | ll141aa | Wrexham | Wrecsam | Froncysyllte STW | 4955 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329154 | 346472 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AB | LL141AB | ll14 1ab | ll141ab | Wrexham | Wrecsam | Froncysyllte STW | 4828 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329172 | 346324 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AD | LL141AD | ll14 1ad | ll141ad | Wrexham | Wrecsam | Froncysyllte STW | 4855 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329239 | 346321 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AE | LL141AE | ll14 1ae | ll141ae | Wrexham | Wrecsam | Froncysyllte STW | 4922 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329237 | 346397 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AF | LL141AF | ll14 1af | ll141af | Wrexham | Wrecsam | Froncysyllte STW | 4857 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329110 | 346384 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AG | LL141AG | ll14 1ag | ll141ag | Wrexham | Wrecsam | Froncysyllte STW | 4829 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329112 | 346353 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AH | LL141AH | ll14 1ah | ll141ah | Wrexham | Wrecsam | Froncysyllte STW | 4859 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329084 | 346398 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AL | LL141AL | ll14 1al | ll141al | Wrexham | Wrecsam | Froncysyllte STW | 4983 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329106 | 346524 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AN | LL141AN | ll14 1an | ll141an | Wrexham | Wrecsam | Froncysyllte STW | 5120 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329150 | 346654 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AP | LL141AP | ll14 1ap | ll141ap | Wrexham | Wrecsam | Froncysyllte STW | 5038 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329087 | 346592 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AR | LL141AR | ll14 1ar | ll141ar | Wrexham | Wrecsam | Froncysyllte STW | 4868 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329016 | 346438 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AS | LL141AS | ll14 1as | ll141as | Wrexham | Wrecsam | Froncysyllte STW | 4900 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328981 | 346487 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AT | LL141AT | ll14 1at | ll141at | Wrexham | Wrecsam | Froncysyllte STW | 4939 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328979 | 346530 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AU | LL141AU | ll14 1au | ll141au | Wrexham | Wrecsam | Froncysyllte STW | 4939 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328938 | 346547 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AW | LL141AW | ll14 1aw | ll141aw | Wrexham | Wrecsam | Froncysyllte STW | 5259 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329190 | 346788 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AY | LL141AY | ll14 1ay | ll141ay | Wrexham | Wrecsam | Froncysyllte STW | 4998 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328968 | 346598 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1AZ | LL141AZ | ll14 1az | ll141az | Wrexham | Wrecsam | Froncysyllte STW | 5118 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329833 | 346292 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BA | LL141BA | ll14 1ba | ll141ba | Wrexham | Wrecsam | Froncysyllte STW | 5000 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328910 | 346623 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BB | LL141BB | ll14 1bb | ll141bb | Wrexham | Wrecsam | Froncysyllte STW | 4915 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328903 | 346534 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BD | LL141BD | ll14 1bd | ll141bd | Wrexham | Wrecsam | Froncysyllte STW | 4876 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328870 | 346505 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BE | LL141BE | ll14 1be | ll141be | Wrexham | Wrecsam | Froncysyllte STW | 4892 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328861 | 346526 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BF | LL141BF | ll14 1bf | ll141bf | Wrexham | Wrecsam | Froncysyllte STW | 5101 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329113 | 346649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BG | LL141BG | ll14 1bg | ll141bg | Wrexham | Wrecsam | Froncysyllte STW | 4935 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328886 | 346563 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BH | LL141BH | ll14 1bh | ll141bh | Wrexham | Wrecsam | Froncysyllte STW | 5015 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328922 | 346634 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BJ | LL141BJ | ll14 1bj | ll141bj | Wrexham | Wrecsam | Froncysyllte STW | 4968 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328902 | 346592 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BL | LL141BL | ll14 1bl | ll141bl | Wrexham | Wrecsam | Froncysyllte STW | 5063 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328948 | 346676 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BN | LL141BN | ll14 1bn | ll141bn | Wrexham | Wrecsam | Froncysyllte STW | 5076 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329070 | 346640 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BP | LL141BP | ll14 1bp | ll141bp | Wrexham | Wrecsam | Froncysyllte STW | 5163 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329058 | 346739 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BQ | LL141BQ | ll14 1bq | ll141bq | Wrexham | Wrecsam | Froncysyllte STW | 4976 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328928 | 346590 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BS | LL141BS | ll14 1bs | ll141bs | Wrexham | Wrecsam | Froncysyllte STW | 5132 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329048 | 346710 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BT | LL141BT | ll14 1bt | ll141bt | Wrexham | Wrecsam | Froncysyllte STW | 5214 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329029 | 346806 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BU | LL141BU | ll14 1bu | ll141bu | Wrexham | Wrecsam | Froncysyllte STW | 5280 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329139 | 346833 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BW | LL141BW | ll14 1bw | ll141bw | Wrexham | Wrecsam | Froncysyllte STW | 5157 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329105 | 346714 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BX | LL141BX | ll14 1bx | ll141bx | Wrexham | Wrecsam | Froncysyllte STW | 5258 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329074 | 346835 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BY | LL141BY | ll14 1by | ll141by | Wrexham | Wrecsam | Froncysyllte STW | 5326 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329284 | 346820 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1BZ | LL141BZ | ll14 1bz | ll141bz | Wrexham | Wrecsam | Froncysyllte STW | 5237 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329112 | 346797 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DA | LL141DA | ll14 1da | ll141da | Wrexham | Wrecsam | Froncysyllte STW | 5250 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329015 | 346850 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DB | LL141DB | ll14 1db | ll141db | Wrexham | Wrecsam | Froncysyllte STW | 5292 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329034 | 346888 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DD | LL141DD | ll14 1dd | ll141dd | Wrexham | Wrecsam | Froncysyllte STW | 5316 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329067 | 346901 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DE | LL141DE | ll14 1de | ll141de | Wrexham | Wrecsam | Froncysyllte STW | 5165 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329189 | 346686 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DF | LL141DF | ll14 1df | ll141df | Wrexham | Wrecsam | Froncysyllte STW | 5190 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329224 | 346698 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DH | LL141DH | ll14 1dh | ll141dh | Wrexham | Wrecsam | Froncysyllte STW | 5060 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329173 | 346578 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DJ | LL141DJ | ll14 1dj | ll141dj | Wrexham | Wrecsam | Froncysyllte STW | 5061 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329191 | 346572 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DL | LL141DL | ll14 1dl | ll141dl | Wrexham | Wrecsam | Froncysyllte STW | 5302 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328998 | 346913 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DP | LL141DP | ll14 1dp | ll141dp | Wrexham | Wrecsam | Froncysyllte STW | 5135 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329189 | 346653 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DQ | LL141DQ | ll14 1dq | ll141dq | Wrexham | Wrecsam | Froncysyllte STW | 5247 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329249 | 346749 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DT | LL141DT | ll14 1dt | ll141dt | Wrexham | Wrecsam | Froncysyllte STW | 5212 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329207 | 346730 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DU | LL141DU | ll14 1du | ll141du | Wrexham | Wrecsam | Froncysyllte STW | 5263 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329330 | 346730 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1DY | LL141DY | ll14 1dy | ll141dy | Wrexham | Wrecsam | Froncysyllte STW | 5336 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329404 | 346776 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EA | LL141EA | ll14 1ea | ll141ea | Wrexham | Wrecsam | Froncysyllte STW | 5277 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329226 | 346792 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EB | LL141EB | ll14 1eb | ll141eb | Wrexham | Wrecsam | Froncysyllte STW | 5295 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329285 | 346786 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1ED | LL141ED | ll14 1ed | ll141ed | Wrexham | Wrecsam | Froncysyllte STW | 5309 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329315 | 346787 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EE | LL141EE | ll14 1ee | ll141ee | Wrexham | Wrecsam | Froncysyllte STW | 5332 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329344 | 346800 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EF | LL141EF | ll14 1ef | ll141ef | Wrexham | Wrecsam | Froncysyllte STW | 5362 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329409 | 346802 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EG | LL141EG | ll14 1eg | ll141eg | Wrexham | Wrecsam | Froncysyllte STW | 5371 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329374 | 346828 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EH | LL141EH | ll14 1eh | ll141eh | Wrexham | Wrecsam | Froncysyllte STW | 5419 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329144 | 346981 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EJ | LL141EJ | ll14 1ej | ll141ej | Wrexham | Wrecsam | Froncysyllte STW | 5391 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329136 | 346954 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EL | LL141EL | ll14 1el | ll141el | Wrexham | Wrecsam | Froncysyllte STW | 5382 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329252 | 346895 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EN | LL141EN | ll14 1en | ll141en | Wrexham | Wrecsam | Froncysyllte STW | 5343 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329288 | 346837 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EP | LL141EP | ll14 1ep | ll141ep | Wrexham | Wrecsam | Froncysyllte STW | 5445 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329589 | 346806 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1ER | LL141ER | ll14 1er | ll141er | Wrexham | Wrecsam | Froncysyllte STW | 5469 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329393 | 346928 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1ES | LL141ES | ll14 1es | ll141es | Wrexham | Wrecsam | Froncysyllte STW | 5462 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329449 | 346894 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1ET | LL141ET | ll14 1et | ll141et | Wrexham | Wrecsam | Froncysyllte STW | 5526 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329537 | 346923 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EU | LL141EU | ll14 1eu | ll141eu | Wrexham | Wrecsam | Froncysyllte STW | 5456 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329582 | 346822 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EW | LL141EW | ll14 1ew | ll141ew | Wrexham | Wrecsam | Froncysyllte STW | 5416 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329485 | 346826 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1EY | LL141EY | ll14 1ey | ll141ey | Wrexham | Wrecsam | Froncysyllte STW | 5444 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329596 | 346801 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HA | LL141HA | ll14 1ha | ll141ha | Wrexham | Wrecsam | Froncysyllte STW | 5524 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329623 | 346877 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HB | LL141HB | ll14 1hb | ll141hb | Wrexham | Wrecsam | Froncysyllte STW | 5565 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329583 | 346943 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HD | LL141HD | ll14 1hd | ll141hd | Wrexham | Wrecsam | Froncysyllte STW | 5661 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329654 | 347015 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HE | LL141HE | ll14 1he | ll141he | Wrexham | Wrecsam | Froncysyllte STW | 5650 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329544 | 347057 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HF | LL141HF | ll14 1hf | ll141hf | Wrexham | Wrecsam | Froncysyllte STW | 5689 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329621 | 347063 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HH | LL141HH | ll14 1hh | ll141hh | Wrexham | Wrecsam | Froncysyllte STW | 5639 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329747 | 346942 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HL | LL141HL | ll14 1hl | ll141hl | Wrexham | Wrecsam | Froncysyllte STW | 5514 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329746 | 346801 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HN | LL141HN | ll14 1hn | ll141hn | Wrexham | Wrecsam | Froncysyllte STW | 5523 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329772 | 346797 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HP | LL141HP | ll14 1hp | ll141hp | Wrexham | Wrecsam | Froncysyllte STW | 5443 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329724 | 346732 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HQ | LL141HQ | ll14 1hq | ll141hq | Wrexham | Wrecsam | Froncysyllte STW | 5667 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329832 | 346928 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HR | LL141HR | ll14 1hr | ll141hr | Wrexham | Wrecsam | Froncysyllte STW | 5475 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329664 | 346801 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HS | LL141HS | ll14 1hs | ll141hs | Wrexham | Wrecsam | Froncysyllte STW | 5578 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329685 | 346906 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HT | LL141HT | ll14 1ht | ll141ht | Wrexham | Wrecsam | Froncysyllte STW | 5499 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329655 | 346832 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HU | LL141HU | ll14 1hu | ll141hu | Wrexham | Wrecsam | Froncysyllte STW | 5442 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329680 | 346755 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HW | LL141HW | ll14 1hw | ll141hw | Wrexham | Wrecsam | Froncysyllte STW | 5504 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329765 | 346779 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HX | LL141HX | ll14 1hx | ll141hx | Wrexham | Wrecsam | Froncysyllte STW | 5499 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329576 | 346873 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1HY | LL141HY | ll14 1hy | ll141hy | Wrexham | Wrecsam | Froncysyllte STW | 5538 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329665 | 346871 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1LA | LL141LA | ll14 1la | ll141la | Wrexham | Wrecsam | Froncysyllte STW | 5729 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329686 | 347075 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1LB | LL141LB | ll14 1lb | ll141lb | Wrexham | Wrecsam | Froncysyllte STW | 5512 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329781 | 346780 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1LD | LL141LD | ll14 1ld | ll141ld | Wrexham | Wrecsam | Froncysyllte STW | 5421 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329695 | 346723 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1LE | LL141LE | ll14 1le | ll141le | Wrexham | Wrecsam | Froncysyllte STW | 5646 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329587 | 347032 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1LN | LL141LN | ll14 1ln | ll141ln | Wrexham | Wrecsam | Froncysyllte STW | 4815 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329285 | 346254 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1LP | LL141LP | ll14 1lp | ll141lp | Wrexham | Wrecsam | Froncysyllte STW | 4982 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329587 | 346281 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1LR | LL141LR | ll14 1lr | ll141lr | Wrexham | Wrecsam | Froncysyllte STW | 4761 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329361 | 346154 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1LS | LL141LS | ll14 1ls | ll141ls | Wrexham | Wrecsam | Froncysyllte STW | 5096 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329752 | 346316 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1LT | LL141LT | ll14 1lt | ll141lt | Wrexham | Wrecsam | Froncysyllte STW | 5197 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329894 | 346346 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1LW | LL141LW | ll14 1lw | ll141lw | Wrexham | Wrecsam | Froncysyllte STW | 4916 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329454 | 346279 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1LY | LL141LY | ll14 1ly | ll141ly | Wrexham | Wrecsam | Froncysyllte STW | 5138 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329762 | 346359 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NA | LL141NA | ll14 1na | ll141na | Wrexham | Wrecsam | Froncysyllte STW | 5299 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330053 | 346365 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NB | LL141NB | ll14 1nb | ll141nb | Wrexham | Wrecsam | Froncysyllte STW | 5246 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329974 | 346353 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1ND | LL141ND | ll14 1nd | ll141nd | Wrexham | Wrecsam | Froncysyllte STW | 5254 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330053 | 346310 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NE | LL141NE | ll14 1ne | ll141ne | Wrexham | Wrecsam | Froncysyllte STW | 5138 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329994 | 346210 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NF | LL141NF | ll14 1nf | ll141nf | Wrexham | Wrecsam | Froncysyllte STW | 5160 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329962 | 346258 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NG | LL141NG | ll14 1ng | ll141ng | Wrexham | Wrecsam | Froncysyllte STW | 5234 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329996 | 346324 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NH | LL141NH | ll14 1nh | ll141nh | Wrexham | Wrecsam | Froncysyllte STW | 5224 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330058 | 346270 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NJ | LL141NJ | ll14 1nj | ll141nj | Wrexham | Wrecsam | Froncysyllte STW | 5239 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330087 | 346269 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NL | LL141NL | ll14 1nl | ll141nl | Wrexham | Wrecsam | Froncysyllte STW | 5217 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330009 | 346295 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NN | LL141NN | ll14 1nn | ll141nn | Wrexham | Wrecsam | Froncysyllte STW | 5192 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329962 | 346297 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NP | LL141NP | ll14 1np | ll141np | Wrexham | Wrecsam | Froncysyllte STW | 5499 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 330030 | 346618 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NQ | LL141NQ | ll14 1nq | ll141nq | Wrexham | Wrecsam | Froncysyllte STW | 5246 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330052 | 346301 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NR | LL141NR | ll14 1nr | ll141nr | Wrexham | Wrecsam | Froncysyllte STW | 5469 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 330031 | 346581 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NS | LL141NS | ll14 1ns | ll141ns | Wrexham | Wrecsam | Froncysyllte STW | 5356 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330059 | 346429 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NT | LL141NT | ll14 1nt | ll141nt | Wrexham | Wrecsam | Froncysyllte STW | 5363 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330045 | 346447 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NU | LL141NU | ll14 1nu | ll141nu | Wrexham | Wrecsam | Froncysyllte STW | 5377 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330086 | 346436 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NW | LL141NW | ll14 1nw | ll141nw | Wrexham | Wrecsam | Froncysyllte STW | 5327 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329999 | 346433 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1NY | LL141NY | ll14 1ny | ll141ny | Wrexham | Wrecsam | Froncysyllte STW | 5417 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330087 | 346484 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PA | LL141PA | ll14 1pa | ll141pa | Wrexham | Wrecsam | Froncysyllte STW | 5518 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 330107 | 346591 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PB | LL141PB | ll14 1pb | ll141pb | Wrexham | Wrecsam | Froncysyllte STW | 5563 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 330066 | 346670 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PE | LL141PE | ll14 1pe | ll141pe | Wrexham | Wrecsam | Froncysyllte STW | 6039 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 330235 | 347125 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PF | LL141PF | ll14 1pf | ll141pf | Wrexham | Wrecsam | Froncysyllte STW | 5610 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329912 | 346818 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PG | LL141PG | ll14 1pg | ll141pg | Wrexham | Wrecsam | Froncysyllte STW | 5756 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 330123 | 346862 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PH | LL141PH | ll14 1ph | ll141ph | Wrexham | Wrecsam | Froncysyllte STW | 5315 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330042 | 346391 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PL | LL141PL | ll14 1pl | ll141pl | Wrexham | Wrecsam | Froncysyllte STW | 5799 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 330060 | 346950 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PN | LL141PN | ll14 1pn | ll141pn | Wrexham | Wrecsam | Froncysyllte STW | 5525 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329808 | 346779 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PP | LL141PP | ll14 1pp | ll141pp | Wrexham | Wrecsam | Froncysyllte STW | 5348 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330224 | 346306 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PQ | LL141PQ | ll14 1pq | ll141pq | Wrexham | Wrecsam | Froncysyllte STW | 5560 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330334 | 346488 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PR | LL141PR | ll14 1pr | ll141pr | Wrexham | Wrecsam | Froncysyllte STW | 5606 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 330389 | 346505 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PS | LL141PS | ll14 1ps | ll141ps | Wrexham | Wrecsam | Froncysyllte STW | 5465 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330201 | 346465 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PT | LL141PT | ll14 1pt | ll141pt | Wrexham | Wrecsam | Froncysyllte STW | 4791 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329184 | 346277 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PU | LL141PU | ll14 1pu | ll141pu | Wrexham | Wrecsam | Froncysyllte STW | 4819 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329242 | 346280 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PW | LL141PW | ll14 1pw | ll141pw | Wrexham | Wrecsam | Froncysyllte STW | 5456 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330292 | 346390 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1PY | LL141PY | ll14 1py | ll141py | Wrexham | Wrecsam | Froncysyllte STW | 4915 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329293 | 346362 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RA | LL141RA | ll14 1ra | ll141ra | Wrexham | Wrecsam | Froncysyllte STW | 5382 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330357 | 346250 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RB | LL141RB | ll14 1rb | ll141rb | Wrexham | Wrecsam | Froncysyllte STW | 5031 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329258 | 346507 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RD | LL141RD | ll14 1rd | ll141rd | Wrexham | Wrecsam | Froncysyllte STW | 5024 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329154 | 346548 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RE | LL141RE | ll14 1re | ll141re | Wrexham | Wrecsam | Froncysyllte STW | 5125 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329248 | 346616 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RF | LL141RF | ll14 1rf | ll141rf | Wrexham | Wrecsam | Froncysyllte STW | 5198 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329254 | 346693 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RG | LL141RG | ll14 1rg | ll141rg | Wrexham | Wrecsam | Froncysyllte STW | 5100 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329274 | 346576 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RH | LL141RH | ll14 1rh | ll141rh | Wrexham | Wrecsam | Froncysyllte STW | 5203 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329321 | 346668 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RJ | LL141RJ | ll14 1rj | ll141rj | Wrexham | Wrecsam | Froncysyllte STW | 5453 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330405 | 346302 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RL | LL141RL | ll14 1rl | ll141rl | Wrexham | Wrecsam | Froncysyllte STW | 5258 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329392 | 346695 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RN | LL141RN | ll14 1rn | ll141rn | Wrexham | Wrecsam | Froncysyllte STW | 5293 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329422 | 346719 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RP | LL141RP | ll14 1rp | ll141rp | Wrexham | Wrecsam | Froncysyllte STW | 5364 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329525 | 346748 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RS | LL141RS | ll14 1rs | ll141rs | Wrexham | Wrecsam | Froncysyllte STW | 5303 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329574 | 346654 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RT | LL141RT | ll14 1rt | ll141rt | Wrexham | Wrecsam | Froncysyllte STW | 5269 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329628 | 346586 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RU | LL141RU | ll14 1ru | ll141ru | Wrexham | Wrecsam | Froncysyllte STW | 5328 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329664 | 346634 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RW | LL141RW | ll14 1rw | ll141rw | Wrexham | Wrecsam | Froncysyllte STW | 5400 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 329498 | 346801 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RX | LL141RX | ll14 1rx | ll141rx | Wrexham | Wrecsam | Froncysyllte STW | 5304 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329538 | 346674 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1RY | LL141RY | ll14 1ry | ll141ry | Wrexham | Wrecsam | Froncysyllte STW | 5349 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329631 | 346676 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SA | LL141SA | ll14 1sa | ll141sa | Wrexham | Wrecsam | Froncysyllte STW | 5360 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329607 | 346701 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SB | LL141SB | ll14 1sb | ll141sb | Wrexham | Wrecsam | Froncysyllte STW | 5389 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329596 | 346739 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SD | LL141SD | ll14 1sd | ll141sd | Wrexham | Wrecsam | Froncysyllte STW | 5223 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329759 | 346459 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SE | LL141SE | ll14 1se | ll141se | Wrexham | Wrecsam | Froncysyllte STW | 5363 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329655 | 346679 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SF | LL141SF | ll14 1sf | ll141sf | Wrexham | Wrecsam | Froncysyllte STW | 5233 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329744 | 346480 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SH | LL141SH | ll14 1sh | ll141sh | Wrexham | Wrecsam | Froncysyllte STW | 5367 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329692 | 346663 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SL | LL141SL | ll14 1sl | ll141sl | Wrexham | Wrecsam | Froncysyllte STW | 5406 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329815 | 346639 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SN | LL141SN | ll14 1sn | ll141sn | Wrexham | Wrecsam | Froncysyllte STW | 5435 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329840 | 346658 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SP | LL141SP | ll14 1sp | ll141sp | Wrexham | Wrecsam | Froncysyllte STW | 5255 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329809 | 346467 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SR | LL141SR | ll14 1sr | ll141sr | Wrexham | Wrecsam | Froncysyllte STW | 5122 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329653 | 346404 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SS | LL141SS | ll14 1ss | ll141ss | Wrexham | Wrecsam | Froncysyllte STW | 5090 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329602 | 346396 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1ST | LL141ST | ll14 1st | ll141st | Wrexham | Wrecsam | Froncysyllte STW | 4966 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329442 | 346342 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SU | LL141SU | ll14 1su | ll141su | Wrexham | Wrecsam | Froncysyllte STW | 5035 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329444 | 346420 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SW | LL141SW | ll14 1sw | ll141sw | Wrexham | Wrecsam | Froncysyllte STW | 5471 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329866 | 346684 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1SY | LL141SY | ll14 1sy | ll141sy | Wrexham | Wrecsam | Froncysyllte STW | 5059 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329497 | 346418 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TA | LL141TA | ll14 1ta | ll141ta | Wrexham | Wrecsam | Froncysyllte STW | 5435 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 329781 | 346691 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TB | LL141TB | ll14 1tb | ll141tb | Wrexham | Wrecsam | Froncysyllte STW | 4946 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329317 | 346384 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TD | LL141TD | ll14 1td | ll141td | Wrexham | Wrecsam | Froncysyllte STW | 5163 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329675 | 346439 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TE | LL141TE | ll14 1te | ll141te | Wrexham | Wrecsam | Froncysyllte STW | 5006 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329316 | 346452 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TG | LL141TG | ll14 1tg | ll141tg | Wrexham | Wrecsam | Froncysyllte STW | 5065 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328540 | 346817 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TH | LL141TH | ll14 1th | ll141th | Wrexham | Wrecsam | Froncysyllte STW | 5886 | 924 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.22 | 9.19 | 10.15 | 328680 | 347631 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TJ | LL141TJ | ll14 1tj | ll141tj | Wrexham | Wrecsam | Froncysyllte STW | 5128 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328827 | 346790 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TL | LL141TL | ll14 1tl | ll141tl | Wrexham | Wrecsam | Froncysyllte STW | 5784 | 924 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.22 | 9.19 | 10.15 | 328564 | 347556 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TN | LL141TN | ll14 1tn | ll141tn | Wrexham | Wrecsam | Froncysyllte STW | 5787 | 924 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.22 | 9.19 | 10.15 | 328723 | 347516 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TP | LL141TP | ll14 1tp | ll141tp | Wrexham | Wrecsam | Froncysyllte STW | 3015 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 328855 | 344417 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TR | LL141TR | ll14 1tr | ll141tr | Wrexham | Wrecsam | Froncysyllte STW | 3134 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 328923 | 344515 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TS | LL141TS | ll14 1ts | ll141ts | Wrexham | Wrecsam | Froncysyllte STW | 2996 | 884 | 700to900 | 1.77 | 1.29 | 0.95 | 16.48 | 8.79 | 9.71 | 328846 | 344400 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TT | LL141TT | ll14 1tt | ll141tt | Wrexham | Wrecsam | Froncysyllte STW | 2878 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 327892 | 344729 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TU | LL141TU | ll14 1tu | ll141tu | Wrexham | Wrecsam | Froncysyllte STW | 2280 | 915 | 900to1200 | 1.83 | 1.34 | 0.98 | 17.05 | 9.1 | 10.05 | 328224 | 343948 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TW | LL141TW | ll14 1tw | ll141tw | Wrexham | Wrecsam | Froncysyllte STW | 3433 | 896 | 700to900 | 1.79 | 1.31 | 0.96 | 16.7 | 8.91 | 9.84 | 329018 | 344813 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1TY | LL141TY | ll14 1ty | ll141ty | Wrexham | Wrecsam | Froncysyllte STW | 2126 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 327449 | 344058 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UA | LL141UA | ll14 1ua | ll141ua | Wrexham | Wrecsam | Froncysyllte STW | 2536 | 1006 | 900to1200 | 2.01 | 1.47 | 1.08 | 18.75 | 10 | 11.05 | 325995 | 344237 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UB | LL141UB | ll14 1ub | ll141ub | Wrexham | Wrecsam | Froncysyllte STW | 2969 | 979 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.25 | 9.73 | 10.76 | 326520 | 344869 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UE | LL141UE | ll14 1ue | ll141ue | Wrexham | Wrecsam | Froncysyllte STW | 3797 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 327130 | 345756 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UF | LL141UF | ll14 1uf | ll141uf | Wrexham | Wrecsam | Froncysyllte STW | 3569 | 997 | 900to1200 | 2 | 1.46 | 1.07 | 18.58 | 9.91 | 10.95 | 327361 | 345519 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UG | LL141UG | ll14 1ug | ll141ug | Wrexham | Wrecsam | Froncysyllte STW | 4566 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 326910 | 346520 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UH | LL141UH | ll14 1uh | ll141uh | Wrexham | Wrecsam | Froncysyllte STW | 5455 | 1031 | 900to1200 | 2.06 | 1.51 | 1.11 | 19.22 | 10.25 | 11.33 | 326638 | 347393 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UJ | LL141UJ | ll14 1uj | ll141uj | Wrexham | Wrecsam | Froncysyllte STW | 5156 | 977 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.21 | 9.71 | 10.73 | 327597 | 347091 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UL | LL141UL | ll14 1ul | ll141ul | Wrexham | Wrecsam | Froncysyllte STW | 5195 | 977 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.21 | 9.71 | 10.73 | 327540 | 347135 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UN | LL141UN | ll14 1un | ll141un | Wrexham | Wrecsam | Froncysyllte STW | 4670 | 977 | 900to1200 | 1.96 | 1.43 | 1.05 | 18.21 | 9.71 | 10.73 | 327816 | 346575 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UP | LL141UP | ll14 1up | ll141up | Wrexham | Wrecsam | Froncysyllte STW | 5497 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330352 | 346397 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UR | LL141UR | ll14 1ur | ll141ur | Wrexham | Wrecsam | Froncysyllte STW | 5547 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330487 | 346358 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1US | LL141US | ll14 1us | ll141us | Wrexham | Wrecsam | Froncysyllte STW | 5657 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 330345 | 346599 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UT | LL141UT | ll14 1ut | ll141ut | Wrexham | Wrecsam | Froncysyllte STW | 5555 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330442 | 346403 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UU | LL141UU | ll14 1uu | ll141uu | Wrexham | Wrecsam | Froncysyllte STW | 5519 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330391 | 346396 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UW | LL141UW | ll14 1uw | ll141uw | Wrexham | Wrecsam | Froncysyllte STW | 3880 | 958 | 900to1200 | 1.92 | 1.4 | 1.03 | 17.86 | 9.52 | 10.53 | 327990 | 345738 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1UY | LL141UY | ll14 1uy | ll141uy | Wrexham | Wrecsam | Froncysyllte STW | 5615 | 871 | 700to900 | 1.74 | 1.28 | 0.94 | 16.23 | 8.66 | 9.57 | 330245 | 346616 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1YE | LL141YE | ll14 1ye | ll141ye | Wrexham | Wrecsam | Froncysyllte STW | 5612 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330548 | 346393 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1YF | LL141YF | ll14 1yf | ll141yf | Wrexham | Wrecsam | Froncysyllte STW | 5556 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330538 | 346330 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 1YG | LL141YG | ll14 1yg | ll141yg | Wrexham | Wrecsam | Froncysyllte STW | 5545 | 827 | 700to900 | 1.66 | 1.21 | 0.89 | 15.41 | 8.22 | 9.09 | 330574 | 346287 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AA | LL142AA | ll14 2aa | ll142aa | Wrexham | Wrecsam | Froncysyllte STW | 5085 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329985 | 346152 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AB | LL142AB | ll14 2ab | ll142ab | Wrexham | Wrecsam | Froncysyllte STW | 5050 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330034 | 346075 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AD | LL142AD | ll14 2ad | ll142ad | Wrexham | Wrecsam | Froncysyllte STW | 4982 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330039 | 345988 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AE | LL142AE | ll14 2ae | ll142ae | Wrexham | Wrecsam | Froncysyllte STW | 5123 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330057 | 346149 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AF | LL142AF | ll14 2af | ll142af | Wrexham | Wrecsam | Froncysyllte STW | 5044 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329967 | 346115 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AG | LL142AG | ll14 2ag | ll142ag | Wrexham | Wrecsam | Froncysyllte STW | 4693 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330051 | 345615 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AH | LL142AH | ll14 2ah | ll142ah | Wrexham | Wrecsam | Froncysyllte STW | 4642 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330040 | 345559 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AJ | LL142AJ | ll14 2aj | ll142aj | Wrexham | Wrecsam | Froncysyllte STW | 4658 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329968 | 345636 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AL | LL142AL | ll14 2al | ll142al | Wrexham | Wrecsam | Froncysyllte STW | 5121 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330076 | 346132 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AN | LL142AN | ll14 2an | ll142an | Wrexham | Wrecsam | Froncysyllte STW | 4846 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330030 | 345826 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AP | LL142AP | ll14 2ap | ll142ap | Wrexham | Wrecsam | Cefn Mawr WwTW | 4923 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330271 | 345732 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AR | LL142AR | ll14 2ar | ll142ar | Wrexham | Wrecsam | Froncysyllte STW | 4758 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330153 | 345615 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AS | LL142AS | ll14 2as | ll142as | Wrexham | Wrecsam | Cefn Mawr WwTW | 4851 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330265 | 345649 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AT | LL142AT | ll14 2at | ll142at | Wrexham | Wrecsam | Cefn Mawr WwTW | 4781 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330209 | 345603 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AU | LL142AU | ll14 2au | ll142au | Wrexham | Wrecsam | Froncysyllte STW | 4967 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330219 | 345832 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AW | LL142AW | ll14 2aw | ll142aw | Wrexham | Wrecsam | Froncysyllte STW | 4869 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330180 | 345737 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AX | LL142AX | ll14 2ax | ll142ax | Wrexham | Wrecsam | Froncysyllte STW | 5167 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330085 | 346182 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AY | LL142AY | ll14 2ay | ll142ay | Wrexham | Wrecsam | Froncysyllte STW | 4944 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330132 | 345871 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2AZ | LL142AZ | ll14 2az | ll142az | Wrexham | Wrecsam | Cefn Mawr WwTW | 4721 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330215 | 345525 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BA | LL142BA | ll14 2ba | ll142ba | Wrexham | Wrecsam | Froncysyllte STW | 4910 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330144 | 345818 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BB | LL142BB | ll14 2bb | ll142bb | Wrexham | Wrecsam | Froncysyllte STW | 5083 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330262 | 345945 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BD | LL142BD | ll14 2bd | ll142bd | Wrexham | Wrecsam | Froncysyllte STW | 5108 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330366 | 345893 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BE | LL142BE | ll14 2be | ll142be | Wrexham | Wrecsam | Cefn Mawr WwTW | 4984 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330440 | 345685 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BF | LL142BF | ll14 2bf | ll142bf | Wrexham | Wrecsam | Froncysyllte STW | 4705 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329909 | 345740 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BH | LL142BH | ll14 2bh | ll142bh | Wrexham | Wrecsam | Froncysyllte STW | 5098 | 925 | 900to1200 | 1.85 | 1.35 | 0.99 | 17.24 | 9.19 | 10.16 | 328917 | 346725 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BJ | LL142BJ | ll14 2bj | ll142bj | Wrexham | Wrecsam | Froncysyllte STW | 5034 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 330112 | 345999 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BL | LL142BL | ll14 2bl | ll142bl | Wrexham | Wrecsam | Froncysyllte STW | 4789 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329141 | 346295 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BN | LL142BN | ll14 2bn | ll142bn | Wrexham | Wrecsam | Froncysyllte STW | 4736 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329197 | 346210 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BP | LL142BP | ll14 2bp | ll142bp | Wrexham | Wrecsam | Froncysyllte STW | 4518 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329148 | 345990 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BS | LL142BS | ll14 2bs | ll142bs | Wrexham | Wrecsam | Froncysyllte STW | 4637 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329129 | 346133 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BT | LL142BT | ll14 2bt | ll142bt | Wrexham | Wrecsam | Froncysyllte STW | 4712 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329221 | 346171 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BU | LL142BU | ll14 2bu | ll142bu | Wrexham | Wrecsam | Froncysyllte STW | 4673 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329240 | 346118 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BW | LL142BW | ll14 2bw | ll142bw | Wrexham | Wrecsam | Froncysyllte STW | 4661 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329181 | 346134 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BX | LL142BX | ll14 2bx | ll142bx | Wrexham | Wrecsam | Froncysyllte STW | 4759 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329249 | 346209 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BY | LL142BY | ll14 2by | ll142by | Wrexham | Wrecsam | Froncysyllte STW | 4690 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329345 | 346081 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2BZ | LL142BZ | ll14 2bz | ll142bz | Wrexham | Wrecsam | Froncysyllte STW | 4573 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329188 | 346032 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DA | LL142DA | ll14 2da | ll142da | Wrexham | Wrecsam | Froncysyllte STW | 4479 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329205 | 345917 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DB | LL142DB | ll14 2db | ll142db | Wrexham | Wrecsam | Froncysyllte STW | 4396 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329119 | 345868 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DD | LL142DD | ll14 2dd | ll142dd | Wrexham | Wrecsam | Froncysyllte STW | 4257 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328993 | 345776 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DE | LL142DE | ll14 2de | ll142de | Wrexham | Wrecsam | Froncysyllte STW | 4172 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328935 | 345710 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DF | LL142DF | ll14 2df | ll142df | Wrexham | Wrecsam | Froncysyllte STW | 3987 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328814 | 345563 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DG | LL142DG | ll14 2dg | ll142dg | Wrexham | Wrecsam | Froncysyllte STW | 3971 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328755 | 345573 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DH | LL142DH | ll14 2dh | ll142dh | Wrexham | Wrecsam | Froncysyllte STW | 4094 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328898 | 345641 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DJ | LL142DJ | ll14 2dj | ll142dj | Wrexham | Wrecsam | Froncysyllte STW | 4446 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329156 | 345906 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DL | LL142DL | ll14 2dl | ll142dl | Wrexham | Wrecsam | Froncysyllte STW | 4470 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328884 | 346061 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DN | LL142DN | ll14 2dn | ll142dn | Wrexham | Wrecsam | Froncysyllte STW | 4531 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328842 | 346145 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DP | LL142DP | ll14 2dp | ll142dp | Wrexham | Wrecsam | Froncysyllte STW | 4752 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328857 | 346378 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DQ | LL142DQ | ll14 2dq | ll142dq | Wrexham | Wrecsam | Froncysyllte STW | 4542 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329241 | 345969 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DR | LL142DR | ll14 2dr | ll142dr | Wrexham | Wrecsam | Froncysyllte STW | 4714 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328945 | 346301 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DS | LL142DS | ll14 2ds | ll142ds | Wrexham | Wrecsam | Froncysyllte STW | 4589 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328861 | 346200 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DT | LL142DT | ll14 2dt | ll142dt | Wrexham | Wrecsam | Froncysyllte STW | 4655 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328862 | 346271 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DU | LL142DU | ll14 2du | ll142du | Wrexham | Wrecsam | Froncysyllte STW | 4226 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328931 | 345772 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DW | LL142DW | ll14 2dw | ll142dw | Wrexham | Wrecsam | Froncysyllte STW | 4629 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328779 | 346276 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DX | LL142DX | ll14 2dx | ll142dx | Wrexham | Wrecsam | Froncysyllte STW | 4468 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328763 | 346109 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2DY | LL142DY | ll14 2dy | ll142dy | Wrexham | Wrecsam | Froncysyllte STW | 4694 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329248 | 346137 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EA | LL142EA | ll14 2ea | ll142ea | Wrexham | Wrecsam | Froncysyllte STW | 4564 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328987 | 346119 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EB | LL142EB | ll14 2eb | ll142eb | Wrexham | Wrecsam | Froncysyllte STW | 4539 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328958 | 346104 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2ED | LL142ED | ll14 2ed | ll142ed | Wrexham | Wrecsam | Froncysyllte STW | 4715 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329004 | 346276 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EE | LL142EE | ll14 2ee | ll142ee | Wrexham | Wrecsam | Froncysyllte STW | 4797 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329044 | 346348 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EG | LL142EG | ll14 2eg | ll142eg | Wrexham | Wrecsam | Froncysyllte STW | 3482 | 929 | 900to1200 | 1.86 | 1.36 | 1 | 17.32 | 9.23 | 10.21 | 328496 | 345153 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EH | LL142EH | ll14 2eh | ll142eh | Wrexham | Wrecsam | Froncysyllte STW | 4284 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328904 | 345849 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EJ | LL142EJ | ll14 2ej | ll142ej | Wrexham | Wrecsam | Froncysyllte STW | 4987 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329763 | 346181 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EL | LL142EL | ll14 2el | ll142el | Wrexham | Wrecsam | Froncysyllte STW | 4258 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 328794 | 345869 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EN | LL142EN | ll14 2en | ll142en | Wrexham | Wrecsam | Froncysyllte STW | 4973 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329659 | 346228 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EP | LL142EP | ll14 2ep | ll142ep | Wrexham | Wrecsam | Froncysyllte STW | 4707 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329687 | 345897 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EQ | LL142EQ | ll14 2eq | ll142eq | Wrexham | Wrecsam | Froncysyllte STW | 4856 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329045 | 346412 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2ER | LL142ER | ll14 2er | ll142er | Wrexham | Wrecsam | Froncysyllte STW | 4964 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329629 | 346236 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2ES | LL142ES | ll14 2es | ll142es | Wrexham | Wrecsam | Froncysyllte STW | 4880 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329625 | 346140 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2ET | LL142ET | ll14 2et | ll142et | Wrexham | Wrecsam | Froncysyllte STW | 4813 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329621 | 346064 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EU | LL142EU | ll14 2eu | ll142eu | Wrexham | Wrecsam | Froncysyllte STW | 4871 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329703 | 346081 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EW | LL142EW | ll14 2ew | ll142ew | Wrexham | Wrecsam | Froncysyllte STW | 4841 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329653 | 346077 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2EY | LL142EY | ll14 2ey | ll142ey | Wrexham | Wrecsam | Froncysyllte STW | 4769 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329753 | 345928 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HA | LL142HA | ll14 2ha | ll142ha | Wrexham | Wrecsam | Froncysyllte STW | 4450 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329462 | 345736 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HB | LL142HB | ll14 2hb | ll142hb | Wrexham | Wrecsam | Froncysyllte STW | 4669 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329611 | 345901 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HD | LL142HD | ll14 2hd | ll142hd | Wrexham | Wrecsam | Froncysyllte STW | 4572 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329643 | 345764 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HE | LL142HE | ll14 2he | ll142he | Wrexham | Wrecsam | Froncysyllte STW | 4540 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329577 | 345769 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HF | LL142HF | ll14 2hf | ll142hf | Wrexham | Wrecsam | Froncysyllte STW | 4527 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329450 | 345834 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HG | LL142HG | ll14 2hg | ll142hg | Wrexham | Wrecsam | Froncysyllte STW | 4632 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329548 | 345897 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HH | LL142HH | ll14 2hh | ll142hh | Wrexham | Wrecsam | Froncysyllte STW | 4767 | 869 | 700to900 | 1.74 | 1.27 | 0.93 | 16.2 | 8.64 | 9.55 | 329552 | 346052 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council
LL14 2HL | LL142HL | ll14 2hl | ll142hl | Wrexham | Wrecsam | Froncysyllte STW | 4584 | 910 | 900to1200 | 1.82 | 1.33 | 0.98 | 16.96 | 9.05 | 10 | 329478 | 345883 | Wrexham LPA | NE | River Dee and Bala Lake/ Afon Dyfrdwy a Llyn Tegid | Cyngor Bwrdeistref Sirol Wrecsam | Wrexham County Borough Council